## Nox XV Valves
Nox XV Reliability 2017-15th November 2021
Title | Actual | Comment
Number of Devices | 15 | No of Nox XV's
Number of Days of Data used to Validate Reliability figures | 1779
Total number of Failures in time period to validate | 2 | Nox XV Failures
Total Hrs of Operating Service per Device | 42696 | **=C5*24hrs)
Total Hrs of Operating Service for all devices | 640440 | **=C7*C4 ( green dot indicates enough hrs accumulated to catch 3x MTBF's)
MTBF (in hrs) | 320218 | **=(C8-C15)/C6 (in Hrs)-- (Total hrs of operation- total hrs MTTR)/number of failure (Note this accounts for downtime element)
Failure rate (per hr) | 3.1229e-06 | **=C6/C8 (1/ MTBF)
min hrs history needed for analysis | 960660 | **=1/C10*3 (minimum history is 3 x MTBF)
Calculated Reliability based over Period | 87.52% | **=EXP(-(C10*C7)) Calculated based on interval | Outputs
Calculated Reliability based current failure rated over a 1 Year Period | 97.3% | 8760hrs
Total hrs of use | 640440 | Based on Nox XV's in operation
Total Corrective Maintenance Time to Repair (MTTR) over period (hrs) | 4 | total hrs taken for repairs
Inherent Availability (based on CM works only) Over Period | 100%