## January
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-01-02
Weather: | Dry/overcast
Wind conditions: | Breezy
Air Temperature: | 5 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:27 | 0.4 | 0.6 | 20.4 | 78.6 | 0 | 0 | 998 | 0.89 | 1 | 8.8
BK BH 3 | 10:32 | 0.2 | 1.2 | 19.8 | 78.8 | 0 | 0 | 998 | -0.64 | 1 | 3.1
BK BH 4 | 10:34 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 998 | 0.54 | 1 | 5.1
BK BH 5 | 10:36 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 998 | 0.19 | 1 | 1.5
BK BH 6 | 10:39 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 998 | 0.68 | 1 | 1.5
BK BH 7 | 10:43 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 998 | 0.89 | 1 | 10
BK BH 8 | 10:46 | 29.1 | 1.5 | 18.9 | 50.5 | 0 | 0 | 998 | 0.78 | 32.2 | 3.6
BK BH 9 | 10:52 | 28.9 | 6.8 | 18.1 | 46.2 | 0 | 0 | 998 | 0.88 | 29.6 | 10.4
BK BH 10 | 10:57 | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 998 | 0.98 | 1 | 3.9
BK BH 11 | 11:09 | 0 | 1.3 | 19.4 | 79.3 | 0 | 0 | 998 | -0.85 | 1 | 6.5
BK BH 12 | 11:13 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 998 | 0.58 | 1 | 6.6
BK BH 13 | 11:17 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 998 | -0.88 | 1 | 9.4
BK BH 14 | 11:20 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 998 | 0.62 | 1 | 3.5
BK BH 15 | 11:23 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 998 | 0.84 | 1 | 17.6
BK BH 16 | 11:26 | 0.4 | 1.3 | 18.6 | 79.7 | 0 | 0 | 998 | 1.02 | 1 | 11.4
BK BH 17 | 11:33 | 0 | 1 | 19.3 | 79.7 | 0 | 0 | 998 | 0.91 | 1 | 12.9
BK BH 18 | 9:59 | 0.5 | 2.3 | 19.8 | 77.4 | 0 | 0 | 998 | 0.63 | 6.8 | 21.2
BK BH 19 | 10:03 | 0.6 | 1.5 | 20.4 | 77.5 | 0 | 0 | 998 | 0.9 | 1 | 11.2
BK BH 20 | 10:06 | 0.5 | 6.8 | 17.1 | 75.6 | 0 | 0 | 998 | 0.87 | 1 | 10.7
BK BH 21 | 10:11 | 0.4 | 7.8 | 11.5 | 80.3 | 0 | 0 | 998 | 0.72 | 1 | 21.7
BK BH 23 | 10:16 | 0 | 3.4 | 19.8 | 76.8 | 0 | 0 | 998 | 0.82 | 1 | 7.3
BK BH 24 | 10:19 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 998 | -0.48 | 1 | 1.5
BK BH 25 | 10:23 | 0 | 1.4 | 20.4 | 78.2 | 0 | 0 | 998 | 0.93 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-01-09
Weather: | Dry/overcast
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:22 | 0.5 | 0.6 | 20.3 | 78.6 | 0 | 0 | 997 | 0.89 | 1 | 8.8
BK BH 3 | 10:27 | 0.1 | 1.5 | 20 | 78.4 | 0 | 0 | 997 | -0.64 | 1 | 3.1
BK BH 4 | 10:29 | 0 | 1.7 | 19.7 | 78.6 | 0 | 0 | 997 | 0.52 | 1 | 5.1
BK BH 5 | 10:31 | 0 | 0.9 | 19 | 80.1 | 0 | 0 | 997 | 0.78 | 1 | 1.5
BK BH 6 | 10:34 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 997 | 0.68 | 1 | 1.5
BK BH 7 | 10:38 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 997 | 0.89 | 1 | 10
BK BH 8 | 10:41 | 29.3 | 1.3 | 19.5 | 49.9 | 0 | 0 | 997 | 0.78 | 32.2 | 3.6
BK BH 9 | 10:47 | 29 | 7 | 18.5 | 45.5 | 0 | 0 | 997 | 0.88 | 29.6 | 10.4
BK BH 10 | 10:52 | 0 | 0.7 | 18.9 | 80.4 | 0 | 0 | 997 | 0.98 | 1 | 3.9
BK BH 11 | 11:04 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 997 | -0.85 | 1 | 6.5
BK BH 12 | 11:08 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 997 | 0.58 | 1 | 6.6
BK BH 13 | 11:02 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 997 | -0.88 | 1 | 9.4
BK BH 14 | 11:15 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 997 | 0.62 | 1 | 3.5
BK BH 15 | 11:18 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 997 | 0.84 | 1 | 17.6
BK BH 16 | 11:21 | 0.5 | 1.4 | 18.9 | 79.2 | 0 | 0 | 997 | 1.02 | 1 | 11.4
BK BH 17 | 11:28 | 0 | 1.2 | 19.1 | 79.7 | 0 | 0 | 997 | 0.91 | 1 | 12.9
BK BH 18 | 9:54 | 4 | 2.4 | 19.5 | 74.1 | 0 | 0 | 997 | 0.63 | 6.8 | 21.2
BK BH 19 | 9:58 | 0.7 | 1.4 | 20.2 | 77.7 | 0 | 0 | 997 | 0.9 | 1 | 11.2
BK BH 20 | 10:01 | 0.6 | 6.6 | 17.5 | 75.3 | 0 | 0 | 997 | 0.87 | 1 | 10.7
BK BH 21 | 10:06 | 0.4 | 7.5 | 11.9 | 80.2 | 0 | 0 | 997 | 0.72 | 1 | 21.7
BK BH 23 | 10:11 | 0 | 3.9 | 19.5 | 76.6 | 0 | 0 | 997 | 0.82 | 1 | 7.3
BK BH 24 | 10:14 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | -0.48 | 1 | 1.5
BK BH 25 | 10:18 | 0 | 1.5 | 20.6 | 77.9 | 0 | 0 | 997 | 0.93 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-01-16
Weather: | Dry/overcast
Wind conditions: | Breezy
Air Temperature: | 7 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:42 | 0.3 | 0.7 | 20.4 | 78.6 | 0 | 0 | 1002 | 0.8 | 1 | 8.8
BK BH 3 | 10:47 | 0.2 | 1.9 | 20.3 | 77.6 | 0 | 0 | 1002 | -0.72 | 1 | 3.1
BK BH 4 | 10:49 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1002 | 0.51 | 1 | 5.1
BK BH 5 | 10:52 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1002 | 0.59 | 1 | 1.5
BK BH 6 | 10:54 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1002 | 0.75 | 1 | 1.5
BK BH 7 | 10:58 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 1002 | 0.89 | 1 | 10
BK BH 8 | 11:01 | 29.5 | 1.4 | 19.9 | 49.2 | 0 | 0 | 1002 | 0.75 | 32.2 | 3.6
BK BH 9 | 11:07 | 28.6 | 6.9 | 18.6 | 45.9 | 0 | 0 | 1002 | 0.86 | 29.6 | 10.4
BK BH 10 | 11:12 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1002 | 0.82 | 1 | 3.9
BK BH 11 | 11:14 | 0 | 2.3 | 20.1 | 77.6 | 0 | 0 | 1002 | -0.89 | 1 | 6.5
BK BH 12 | 11:28 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1002 | 0.65 | 1 | 6.6
BK BH 13 | 11:22 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 1002 | -0.92 | 1 | 9.4
BK BH 14 | 11:35 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1002 | 0.48 | 1 | 3.5
BK BH 15 | 11:38 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | 0.71 | 1 | 17.6
BK BH 16 | 11:41 | 0.6 | 1 | 19.6 | 78.8 | 0 | 0 | 1002 | 1.08 | 1 | 11.4
BK BH 17 | 11:48 | 0 | 1.3 | 19.4 | 79.3 | 0 | 0 | 1002 | 0.87 | 1 | 12.9
BK BH 18 | 10:14 | 4.5 | 2.8 | 19.8 | 72.9 | 0 | 0 | 1002 | 0.56 | 6.8 | 21.2
BK BH 19 | 10:18 | 0.8 | 1.5 | 19.6 | 78.1 | 0 | 0 | 1002 | 0.77 | 1 | 11.2
BK BH 20 | 10:21 | 0.9 | 6 | 17.8 | 75.3 | 0 | 0 | 1002 | 0.62 | 1 | 10.7
BK BH 21 | 10:26 | 0.4 | 7.3 | 12.5 | 79.8 | 0 | 0 | 1002 | 0.93 | 1 | 21.7
BK BH 23 | 10:31 | 0 | 4.2 | 19.3 | 76.5 | 0 | 0 | 1002 | 0.47 | 1 | 7.3
BK BH 24 | 10:34 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1002 | -0.63 | 1 | 1.5
BK BH 25 | 10:38 | 0 | 1.3 | 20.4 | 78.3 | 0 | 0 | 1002 | 0.74 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-01-23
Weather: | Slight rain
Wind conditions: | Breezy
Air Temperature: | 6 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:02 | 0.4 | 0.8 | 20.1 | 78.7 | 0 | 0 | 999 | 0.79 | 1 | 8.8
BK BH 3 | 10:07 | 0.3 | 1.8 | 20 | 77.9 | 0 | 0 | 999 | -0.69 | 1 | 3.1
BK BH 4 | 10:09 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 999 | 0.89 | 1 | 5.1
BK BH 5 | 10:11 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 999 | -0.23 | 1 | 1.5
BK BH 6 | 10:14 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 999 | 0.72 | 1 | 1.5
BK BH 7 | 10:18 | 0 | 2.1 | 19.2 | 78.7 | 0 | 0 | 999 | 0.94 | 1 | 10
BK BH 8 | 10:21 | 29.6 | 1.6 | 20 | 48.8 | 0 | 0 | 999 | 0.71 | 32.2 | 3.6
BK BH 9 | 10:27 | 29.1 | 6.1 | 18.7 | 46.1 | 0 | 0 | 999 | 0.9 | 29.6 | 10.4
BK BH 10 | 10:32 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 999 | 0.87 | 1 | 3.9
BK BH 11 | 10:34 | 0 | 2.4 | 20.4 | 77.2 | 0 | 0 | 999 | -0.88 | 1 | 6.5
BK BH 12 | 10:48 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 999 | 0.62 | 1 | 6.6
BK BH 13 | 10:42 | 0 | 2.7 | 20 | 77.3 | 0 | 0 | 999 | -0.97 | 1 | 9.4
BK BH 14 | 10:55 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 999 | 0.56 | 1 | 3.5
BK BH 15 | 10:58 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 999 | 0.74 | 1 | 17.6
BK BH 16 | 11:01 | 0.7 | 1.1 | 19.4 | 78.8 | 0 | 0 | 999 | 1.13 | 1 | 11.4
BK BH 17 | 11:08 | 0 | 1.3 | 19.7 | 79 | 0 | 0 | 999 | 0.99 | 1 | 12.9
BK BH 18 | 9:34 | 4.1 | 2.8 | 19.6 | 73.5 | 0 | 0 | 999 | 0.68 | 6.8 | 21.2
BK BH 19 | 9:38 | 0.9 | 1.2 | 19.6 | 78.3 | 0 | 0 | 999 | 0.81 | 1 | 11.2
BK BH 20 | 9:41 | 0.5 | 5.6 | 18.7 | 75.2 | 0 | 0 | 999 | 0.57 | 1 | 10.7
BK BH 21 | 9:46 | 0.3 | 6.9 | 12.7 | 80.1 | 0 | 0 | 999 | 0.89 | 1 | 21.7
BK BH 23 | 9:51 | 0 | 3.8 | 19.5 | 76.7 | 0 | 0 | 999 | 0.34 | 1 | 7.3
BK BH 24 | 9:54 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | -0.58 | 1 | 1.5
BK BH 25 | 9:58 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 999 | 0.87 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-01-30
Weather: | dry/overcast
Wind conditions: | calm
Air Temperature: | 7 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0.3 | 1 | 19.9 | 78.8 | 0 | 0 | 1004 | 0.69 | 1 | 8.8
BK BH 3 | 10:24 | 0.5 | 1.7 | 19.7 | 78.1 | 0 | 0 | 1004 | -0.48 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1004 | -0.23 | 1 | 5.1
BK BH 5 | 10:28 | 0 | 1.1 | 19.4 | 79.5 | 0 | 0 | 1004 | 0.87 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 1.2 | 20.4 | 78.4 | 0 | 0 | 1004 | 0.72 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 2.3 | 20.3 | 77.4 | 0 | 0 | 1004 | 0.87 | 1 | 10
BK BH 8 | 10:38 | 29.1 | 1.8 | 19.8 | 49.3 | 0 | 0 | 1004 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:44 | 29.3 | 6.9 | 19 | 44.8 | 0 | 0 | 1004 | 0.78 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 1004 | 0.71 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 2.7 | 20.2 | 77.1 | 0 | 0 | 1004 | -0.62 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1004 | 0.47 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 1004 | -0.97 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1004 | 0.48 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 1004 | 0.56 | 1 | 17.6
BK BH 16 | 11:18 | 0.6 | 1.4 | 19.2 | 78.8 | 0 | 0 | 1004 | 1.27 | 1 | 11.4
BK BH 17 | 11:25 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1004 | 0.89 | 1 | 12.9
BK BH 18 | 9:51 | 4.4 | 2.5 | 20.1 | 73 | 0 | 0 | 1004 | 0.59 | 6.8 | 21.2
BK BH 19 | 9:55 | 1.1 | 1.4 | 19.9 | 77.6 | 0 | 0 | 1004 | 0.74 | 1 | 11.2
BK BH 20 | 9:58 | 0.6 | 5.9 | 18.8 | 74.7 | 0 | 0 | 1004 | 0.5 | 1 | 10.7
BK BH 21 | 10:03 | 0.4 | 7.1 | 13 | 79.5 | 0 | 0 | 1004 | 0.56 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 3.5 | 19.2 | 77.3 | 0 | 0 | 1004 | 0.85 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1004 | -0.89 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1004 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-01-09
Weather: |  | Dry/Overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 7 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-03-20
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 11:00 | 47.8 | 31.2 | 1 | 20 | 25 | 27 | 998 | -45.98
GV1 |  | 32.4 | 29.4 | 5.2 | 33 | 16 | 33 | 998 | 1.38 | Left Off
GV2 |  | 30.2 | 29.9 | 3.9 | 36 | 7 | 5 | 998 | 2.34 | Left Off
GV3 |  | 54.8 | 31.8 | 0.5 | 12.9 | 18 | 36 | 998 | -26.87 | Left Open Full
GV4 |  | 41.6 | 33.9 | 1 | 23.5 | 19 | 31 | 998 | -22.38 | left cracked open
GV5+R1 |  | 52.6 | 38.4 | 0.3 | 8.7 | 24 | 50 | 998 | -21.47 | Left Open full
GV6 |  | 51.9 | 36.1 | 0.5 | 11.5 | 19 | 24 | 998 | -19.63 | Left Open Full
GV7 |  | 51.8 | 30.9 | 1.2 | 16.1 | 12 | 6 | 998 | 8.97 | Left Cracked Open
GV8 |  | 43.5 | 35.9 | 1.1 | 19.5 | 20 | 41 | 998 | -4.51 | Left closed half way
GV9 |  | 53 | 35.9 | 0.5 | 10.6 | 19 | 9 | 998 | -19.63 | Left Open Full
GV9.1 |  | 27.8 | 22.9 | 8.2 | 41.1 | 14 | 10 | 998 | -1.24 | Left turned off
GV10 |  | 50 | 23.9 | 1 | 25.1 | 20 | 4 | 998 | -12.4 | Reg cracked open good gas
GV11 |  | 1.7 | 2 | 15.9 | 80.4 | 12 | 6 | 998 | 0.89 | Left Off
GV12+R3 |  | 55.9 | 33.6 | 0.3 | 10.2 | 13 | 17 | 998 | -17.48 | Left Open Full
GV13 |  | 1.1 | 2.7 | 18 | 78.2 | 7 | 9 | 998 | 0.23 | Left Off
GV14 |  | 50.4 | 33.7 | 0.4 | 15.5 | 14 | 36 | 998 | -22.34 | Left Open Full
GV15 |  | 53.1 | 35.6 | 0.7 | 10.6 | 19 | 45 | 998 | -9.98 | Left Open Full
GV16 |  | 51.4 | 32.9 | 0.4 | 15.3 | 10 | 22 | 998 | -12.14 | opened full
GV17+LC4 |  | 53.4 | 31.2 | 0.6 | 14.8 | 12 | 69 | 998 | -4.89 | Open full
GV18+21 |  | 54.2 | 32.5 | 0.5 | 12.8 | 19 | 7 | 998 | -16.24 | Open full
GV19 |  | 34.5 | 26.9 | 5.9 | 32.7 | 11 | 8 | 998 | 1.39 | Left Off
GV20 |  | 0.8 | 2.5 | 15.8 | 80.9 | 13 | 4 | 998 | 0.24 | Left Off
GV 22 + CVs |  | 55.2 | 31.5 | 0.4 | 12.9 | 28 | 52 | 998 | -22.87 | Left Open Full
GV23 |  | 54 | 30.2 | 0.2 | 15.6 | 13 | 53 | 998 | -21.39 | Left Open Full
GV24 |  | 56.3 | 34.1 | 0.3 | 9.3 | 12 | 16 | 998 | -20 | Left Open Full
GV25 |  | 53.7 | 35.9 | 0.4 | 10 | 10 | 17 | 998 | -23.11 | Left Open Full
GV26/A |  | 52 | 34.5 | 0.3 | 13.2 | 14 | 26 | 998 | -16.68 | Left Open Full
GV27+28 / B+C |  | 51.8 | 31.5 | 0.6 | 16.1 | 19 | 22 | 998 | -22.34 | Open full
GV30 |  | 34.5 | 30.2 | 2.3 | 33 | 10 | 31 | 998 | -5.53 | Left OFF
GV31 |  | 54.2 | 32.1 | 0.5 | 13.2 | 7 | 36 | 998 | -16.37 | Open Full
GV32 |  | 53.6 | 33.8 | 0.7 | 11.9 | 5 | 38 | 998 | -14.52 | Open Full
GV33 |  | 41.2 | 30.2 | 1.4 | 27.2 | 3 | 40 | 998 | 1.39 | Left Off bad gas
GV34 |  | 52.6 | 31.2 | 0.5 | 15.7 | 10 | 31 | 998 | -14.72 | Open Full
RP6.1 |  | 10.2 | 13.6 | 11.2 | 65 | 12 | 9 | 998 | 0.56 | Left Off
LC1B |  | 46.5 | 33.6 | 1.1 | 18.8 | 11 | 7 | 998 | -8.31 | Cracked open
LC1.1 |  | 16.5 | 15.9 | 7.9 | 59.7 | 9 | 10 | 998 | 0.69 | Left Off
LC2R? |  | 30.2 | 20.3 | 8.5 | 41 | 14 | 16 | 998 | 0.44 | Left Off
GV 2.1 |  | 54.4 | 32.5 | 0.5 | 12.6 | 29 | 52 | 998 | -13.22 | Left Open Full
GV 2.2+ LC2B |  | 33.5 | 30.2 | 3.6 | 32.7 | 13 | 9 | 998 | 0.78 | Turned Off
GV / LC3.1 + LC3 |  | 49.6 | 24.5 | 1.1 | 24.8 | 16 | 16 | 998 | -5.39 | left cracked open
LC4B |  | 54.6 | 32.5 | 0.4 | 12.5 | 37 | 33 | 998 | -14.42 | Open full
LC5 |  | 50.1 | 30.9 | 4 | 15 | 20 | 78 | 998 | 1.89 | Left off o2 flew up after cracking open
LC6 |  | 52.3 | 25.6 | 0.6 | 21.5 | 17 | 71 | 998 | 0.78 | Reg cracked open good gas
GV29D + LC6B |  | 51.7 | 29.6 | 0.5 | 18.2 | 23 | 62 | 998 | -12.28 | Left Open Full
PW1 |  | 39.6 | 15.2 | 5.5 | 39.7 | 6 | 43 | 998 | 1.52 | Left Off bad gas high o2
PW2 |  | 49.6 | 34.5 | 1.2 | 14.7 | 14 | 78 | 998 | 10.23 | left Cracked Open
PW3 |  | 11.6 | 9.9 | 13.6 | 64.9 | 8 | 0 | 998 | -7.454 | Well Left Off
PW4 |  | 29.6 | 26.3 | 5.9 | 38.2 | 6 | 0 | 998 | 1.59 | left off
PW5 |  | 24.1 | 24.7 | 2.7 | 48.5 | 4 | 4 | 998 | 0.69 | left off
PW6 |  | 51.2 | 32.6 | 0.6 | 15.6 | 9 | 9 | 998 | -14.36 | Left Opened Full
Cap Vent |  | 41.1 | 31.2 | 2 | 25.7 | 8 | 3 | 998 | 0.74 | left off
Flare | 15:23 | 50.9 | 23.6 | 0.7 | 24.8 | 12 | 8 | 998 | -42.17 | Gas improved slightly

## February
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-02-06
Weather: | dry/overcast
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0.4 | 0.9 | 19.7 | 79 | 0 | 0 | 999 | -0.63 | 1 | 8.8
BK BH 3 | 10:41 | 0.6 | 1.2 | 19.8 | 78.4 | 0 | 0 | 999 | -0.25 | 1 | 3.1
BK BH 4 | 10:43 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 999 | -0.45 | 1 | 5.1
BK BH 5 | 10:46 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 999 | -0.28 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 1.4 | 20.2 | 78.4 | 0 | 0 | 999 | -0.65 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 999 | 0.35 | 1 | 10
BK BH 8 | 10:55 | 30.2 | 1.4 | 19.9 | 48.5 | 0 | 0 | 999 | -0.14 | 32.2 | 3.6
BK BH 9 | 11:01 | 29 | 6.7 | 19.7 | 44.6 | 0 | 0 | 999 | 0.25 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.38 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 999 | -0.96 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 999 | 0.15 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 999 | 0.24 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 999 | -0.75 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 2.3 | 20.1 | 77.6 | 0 | 0 | 999 | 0.38 | 1 | 17.6
BK BH 16 | 11:35 | 0.5 | 1.9 | 19.5 | 78.1 | 0 | 0 | 999 | -0.77 | 1 | 11.4
BK BH 17 | 11:42 | 0 | 1.8 | 20.3 | 77.9 | 0 | 0 | 999 | -0.65 | 1 | 12.9
BK BH 18 | 10:08 | 3.9 | 2.2 | 20.4 | 73.5 | 0 | 0 | 999 | -78 | 6.8 | 21.2
BK BH 19 | 10:12 | 0.8 | 1.6 | 19.6 | 78 | 0 | 0 | 999 | 0.63 | 1 | 11.2
BK BH 20 | 10:15 | 0.5 | 5.5 | 19.1 | 74.9 | 0 | 0 | 999 | -0.87 | 1 | 10.7
BK BH 21 | 10:20 | 0.4 | 7.3 | 13.6 | 78.7 | 0 | 0 | 999 | -0.58 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 3.9 | 19.4 | 76.7 | 0 | 0 | 999 | -0.48 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 999 | -0.25 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.86 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-02-13
Weather: | Slight rain
Wind conditions: | Breezy
Air Temperature: | 9 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:15 | 0.3 | 0.6 | 19.9 | 79.2 | 0 | 0 | 1002 | -0.54 | 1 | 8.8
BK BH 3 | 11:20 | 0.4 | 1 | 19.5 | 79.1 | 0 | 0 | 1002 | -0.36 | 1 | 3.1
BK BH 4 | 11:23 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1002 | -0.78 | 1 | 5.1
BK BH 5 | 11:25 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1002 | -0.21 | 1 | 1.5
BK BH 6 | 11:27 | 0 | 1.2 | 20.4 | 78.4 | 0 | 0 | 1002 | 0.95 | 1 | 1.5
BK BH 7 | 11:31 | 0 | 2.8 | 20.3 | 76.9 | 0 | 0 | 1002 | -0.63 | 1 | 10
BK BH 8 | 11:34 | 30.4 | 3.2 | 19.8 | 46.6 | 0 | 0 | 1002 | 0.25 | 32.2 | 3.6
BK BH 9 | 11:40 | 29.2 | 6.2 | 20.1 | 44.5 | 0 | 0 | 1002 | -0.14 | 29.6 | 10.4
BK BH 10 | 11:45 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 1002 | 0.25 | 1 | 3.9
BK BH 11 | 11:57 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1002 | -0.65 | 1 | 6.5
BK BH 12 | 12:01 | 0 | 3.2 | 20.1 | 76.7 | 0 | 0 | 1002 | 0.32 | 1 | 6.6
BK BH 13 | 12:05 | 0 | 2.6 | 19.5 | 77.9 | 0 | 0 | 1002 | -0.17 | 1 | 9.4
BK BH 14 | 12:08 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 1002 | 0.36 | 1 | 3.5
BK BH 15 | 12:11 | 0 | 3.2 | 20.3 | 76.5 | 0 | 0 | 1002 | -0.98 | 1 | 17.6
BK BH 16 | 12:14 | 0.4 | 2.3 | 19.6 | 77.7 | 0 | 0 | 1002 | 0.25 | 1 | 11.4
BK BH 17 | 12:21 | 0 | 1.5 | 20.4 | 78.1 | 0 | 0 | 1002 | -0.11 | 1 | 12.9
BK BH 18 | 10:47 | 3.6 | 2.4 | 20.2 | 73.8 | 0 | 0 | 1002 | 0.75 | 6.8 | 21.2
BK BH 19 | 10:51 | 0.7 | 1.8 | 19.9 | 77.6 | 0 | 0 | 1002 | 0.36 | 1 | 11.2
BK BH 20 | 10:54 | 0.8 | 5.2 | 19.5 | 74.5 | 0 | 0 | 1002 | -0.82 | 1 | 10.7
BK BH 21 | 10:59 | 0.3 | 7 | 14 | 78.7 | 0 | 0 | 1002 | 0.39 | 1 | 21.7
BK BH 23 | 11:04 | 0 | 3.7 | 19.6 | 76.7 | 0 | 0 | 1002 | -0.14 | 1 | 7.3
BK BH 24 | 11:07 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1002 | 0.27 | 1 | 1.5
BK BH 25 | 11:11 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1002 | -0.54 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-02-20
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 11 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:58 | 0.2 | 0.9 | 20 | 78.9 | 0 | 0 | 1001 | 0.49 | 1 | 8.8
BK BH 3 | 11:03 | 0.6 | 1.2 | 19.8 | 78.4 | 0 | 0 | 1001 | -0.62 | 1 | 3.1
BK BH 4 | 11:05 | 0 | 1.8 | 19.7 | 78.5 | 0 | 0 | 1001 | -0.46 | 1 | 5.1
BK BH 5 | 11:07 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 1001 | -0.31 | 1 | 1.5
BK BH 6 | 11:10 | 0 | 1.1 | 20.3 | 78.6 | 0 | 0 | 1001 | 0.75 | 1 | 1.5
BK BH 7 | 11:14 | 0 | 2.3 | 20.1 | 77.6 | 0 | 0 | 1001 | 0.36 | 1 | 10
BK BH 8 | 11:17 | 30.2 | 3.5 | 19.9 | 46.4 | 0 | 0 | 1001 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:23 | 29.1 | 6 | 20.4 | 44.5 | 0 | 0 | 1001 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:28 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1001 | 0.69 | 1 | 3.9
BK BH 11 | 11:40 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 1001 | -0.15 | 1 | 6.5
BK BH 12 | 11:44 | 0 | 3.2 | 20.4 | 76.4 | 0 | 0 | 1001 | 0.24 | 1 | 6.6
BK BH 13 | 11:48 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1001 | -0.63 | 1 | 9.4
BK BH 14 | 11:51 | 0 | 1.8 | 20.4 | 77.8 | 0 | 0 | 1001 | 0.21 | 1 | 3.5
BK BH 15 | 11:54 | 0 | 3 | 20.1 | 76.9 | 0 | 0 | 1001 | 0.02 | 1 | 17.6
BK BH 16 | 11:57 | 0.3 | 2.1 | 19.2 | 78.4 | 0 | 0 | 1001 | 0.58 | 1 | 11.4
BK BH 17 | 12:04 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1001 | 0.77 | 1 | 12.9
BK BH 18 | 10:30 | 3.9 | 2 | 20.1 | 74 | 0 | 0 | 1001 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:34 | 0.5 | 1.5 | 19.6 | 78.4 | 0 | 0 | 1001 | 0.38 | 1 | 11.2
BK BH 20 | 10:37 | 0.6 | 5.8 | 19.2 | 74.4 | 0 | 0 | 1001 | -0.25 | 1 | 10.7
BK BH 21 | 10:42 | 0.2 | 7.4 | 14.5 | 77.9 | 0 | 0 | 1001 | 0.14 | 1 | 21.7
BK BH 23 | 10:47 | 0 | 3.5 | 19.2 | 77.3 | 0 | 0 | 1001 | 0.75 | 1 | 7.3
BK BH 24 | 10:50 | 0 | 1.1 | 20.3 | 78.6 | 0 | 0 | 1001 | -0.63 | 1 | 1.5
BK BH 25 | 10:54 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1001 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-02-27
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 10 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0.3 | 1 | 20.1 | 78.6 | 0 | 0 | 998 | 0.42 | 1 | 8.8
BK BH 3 | 10:28 | 0.7 | 1.6 | 20.3 | 77.4 | 0 | 0 | 998 | 0.75 | 1 | 3.1
BK BH 4 | 10:30 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 998 | 0.12 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 998 | 0.29 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 1 | 20.4 | 78.6 | 0 | 0 | 998 | -0.23 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 2.6 | 20.2 | 77.2 | 0 | 0 | 998 | 0.14 | 1 | 10
BK BH 8 | 10:42 | 30 | 3.2 | 19.6 | 47.2 | 0 | 0 | 998 | -0.53 | 32.2 | 3.6
BK BH 9 | 10:48 | 29 | 5.9 | 20.2 | 44.9 | 0 | 0 | 998 | 0.26 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 998 | -0.75 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 2.7 | 20 | 77.3 | 0 | 0 | 998 | 0.14 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 3 | 20.5 | 76.5 | 0 | 0 | 998 | -0.77 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 2 | 19 | 79 | 0 | 0 | 998 | 0.56 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 998 | 0.34 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 3.8 | 19.6 | 76.6 | 0 | 0 | 998 | -0.15 | 1 | 17.6
BK BH 16 | 11:22 | 0.2 | 2.3 | 19.5 | 78 | 0 | 0 | 998 | 0.26 | 1 | 11.4
BK BH 17 | 11:29 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 998 | 0.31 | 1 | 12.9
BK BH 18 | 9:55 | 3.5 | 2.3 | 20.3 | 73.9 | 0 | 0 | 998 | 0.87 | 6.8 | 21.2
BK BH 19 | 9:59 | 0.6 | 1.9 | 19.7 | 77.8 | 0 | 0 | 998 | 0.9 | 1 | 11.2
BK BH 20 | 10:02 | 0.7 | 5.2 | 19.4 | 74.7 | 0 | 0 | 998 | -0.75 | 1 | 10.7
BK BH 21 | 10:07 | 0.3 | 7.1 | 14.9 | 77.7 | 0 | 0 | 998 | -0.14 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 3.2 | 19.5 | 77.3 | 0 | 0 | 998 | 0.21 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 1 | 20.6 | 78.4 | 0 | 0 | 998 | 0.68 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 998 | -0.71 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-02-12
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 10 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-03-20
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:50 | 46.2 | 29.2 | 0.8 | 23.8 | 27 | 22 | 999 | -45.98
GV1 |  | 31.2 | 31.6 | 4.9 | 32.3 | 18 | 30 | 999 | 1.38 | Left Off
GV2 |  | 30 | 30.2 | 4.2 | 35.6 | 9 | 9 | 999 | 3.25 | Left Off
GV3 |  | 55.2 | 30.7 | 0.9 | 13.2 | 22 | 32 | 999 | -28 | Left Open Full
GV4 |  | 44.8 | 30.2 | 0.9 | 24.1 | 14 | 29 | 999 | -24 | left cracked open
GV5+R1 |  | 50.9 | 36.9 | 0.4 | 11.8 | 20 | 45 | 999 | -32 | Left Open full
GV6 |  | 54.8 | 35.2 | 0.6 | 9.4 | 17 | 21 | 999 | -21 | Left Open Full
GV7 |  | 50.7 | 31.2 | 1.1 | 17 | 16 | 9 | 999 | -4 | Left Cracked Open
GV8 |  | 41.3 | 32.5 | 0.5 | 25.7 | 18 | 36 | 999 | -4.51 | Left closed half way
GV9 |  | 50.1 | 33.6 | 0.3 | 16 | 20 | 12 | 999 | -25 | Left Open Full
GV9.1 |  | 25.6 | 20.1 | 7.4 | 46.9 | 19 | 16 | 999 | -1.24 | Left turned off
GV10 |  | 39.4 | 20.3 | 1.2 | 39.1 | 20 | 9 | 999 | 1.25 | Reg closed bad gas
GV11 |  | 52.2 | 27.1 | 1 | 19.7 | 13 | 7 | 999 | 0.89 | Reg cracked open good gas
GV12+R3 |  | 54.2 | 30.4 | 0.5 | 14.9 | 14 | 15 | 999 | -22 | Left Open Full
GV13 |  | 1.8 | 3.6 | 20.2 | 74.4 | 1 | 10 | 999 | 0.35 | Left Off
GV14 |  | 51.2 | 30.8 | 0.5 | 17.5 | 16 | 36 | 999 | -25 | Left Open Full
GV15 |  | 52.3 | 30.4 | 0.3 | 17 | 23 | 42 | 999 | -11 | Left Open Full
GV16 |  | 52.2 | 30.6 | 0.3 | 16.9 | 7 | 19 | 999 | -12.14 | opened full
GV17+LC4 |  | 54.4 | 33.5 | 0.2 | 11.9 | 12 | 59 | 999 | -5.24 | Open full
GV18+21 |  | 54 | 30.7 | 0.5 | 14.8 | 15 | 8 | 999 | -15.69 | Open full
GV19 |  | 30.2 | 21.4 | 6.2 | 42.2 | 13 | 8 | 999 | 1.89 | Left Off
GV20 |  | 1.2 | 3.6 | 13.2 | 82 | 11 | 9 | 999 | 0.39 | Left Off
GV 22 + CVs |  | 52.3 | 30.2 | 0.3 | 17.2 | 22 | 50 | 999 | -25.69 | Left Open Full
GV23 |  | 54.4 | 31.4 | 0.1 | 14.1 | 16 | 59 | 999 | -30 | Left Open Full
GV24 |  | 55.3 | 33.6 | 0.2 | 10.9 | 14 | 15 | 999 | -15 | Left Open Full
GV25 |  | 54.9 | 30.8 | 0.6 | 13.7 | 11 | 18 | 999 | -17 | Left Open Full
GV26/A |  | 50.2 | 30.9 | 0.4 | 18.5 | 16 | 17 | 999 | -32 | Left Open Full
GV27+28 / B+C |  | 52.3 | 31.5 | 0.6 | 15.6 | 23 | 23 | 999 | -25 | Open full
GV30 |  | 30.5 | 29.6 | 3.9 | 36 | 9 | 29 | 999 | -6 | Left OFF
GV31 |  | 53.9 | 29.3 | 0.4 | 16.4 | 8 | 39 | 999 | -18 | Open Full
GV32 |  | 50.2 | 32.4 | 0.6 | 16.8 | 6 | 35 | 999 | -16 | Open Full
GV33 |  | 43.6 | 28.7 | 1.8 | 25.9 | 4 | 19 | 999 | 1.39 | Left Off bad gas
GV34 |  | 53.2 | 32.9 | 0.4 | 13.5 | 12 | 25 | 999 | -15.68 | Open Full
RP6.1 |  | 11.2 | 14.7 | 9.3 | 64.8 | 16 | 16 | 999 | 0.56 | Left Off
LC1B |  | 44.1 | 27.8 | 1.9 | 26.2 | 10 | 9 | 999 | 1.23 | Reg closed high o2
LC1.1 |  | 19.3 | 16.8 | 5.3 | 58.6 | 8 | 23 | 999 | 0.69 | Left Off
LC2R? |  | 28.4 | 19.3 | 7.9 | 44.4 | 11 | 14 | 999 | 0.89 | Left Off
GV 2.1 |  | 56.3 | 31.2 | 0.4 | 12.1 | 23 | 52 | 999 | -18.92 | Left Open Full
GV 2.2+ LC2B |  | 34.7 | 29.6 | 3.9 | 31.8 | 21 | 9 | 999 | 0.79 | Turned Off
GV / LC3.1 + LC3 |  | 49.6 | 23.7 | 0.9 | 25.8 | 18 | 16 | 999 | -4.52 | left cracked open
LC4B |  | 52.8 | 29.7 | 0.5 | 17 | 45 | 35 | 999 | -24 | Open full
LC5 |  | 49.8 | 29.3 | 3.5 | 17.4 | 19 | 71 | 999 | 1.58 | Left off o2 flew up after cracking open
LC6 |  | 50.3 | 27.4 | 1.5 | 20.8 | 12 | 63 | 999 | 1.24 | Reg closed high o2
GV29D + LC6B |  | 54.2 | 25.7 | 0.6 | 19.5 | 21 | 52 | 999 | -26 | Left Open Full
PW1 |  | 40 | 14.5 | 4.9 | 40.6 | 9 | 48 | 999 | 1.89 | Left Off bad gas high o2
PW2 |  | 50.2 | 33.6 | 1.2 | 15 | 12 | 89 | 999 | 10.23 | left Cracked Open
PW3 |  | 15.8 | 11.4 | 10.2 | 62.6 | 7 | 3 | 999 | -8 | Well Left Off
PW4 |  | 30.2 | 24.1 | 5.3 | 40.4 | 8 | 4 | 999 | 1.59 | left off
PW5 |  | 25.8 | 28.7 | 2.1 | 43.4 | 9 | 9 | 999 | 0.69 | left off
PW6 |  | 50.2 | 30.7 | 0.5 | 18.6 | 12 | 12 | 999 | -14.36 | Left Opened Full
Cap Vent |  | 45.8 | 33.4 | 2.5 | 18.3 | 7 | 8 | 999 | 0.74 | left off
Flare | 15:05 | 54.9 | 24.5 | 0.5 | 20.1 | 16 | 12 | 999 | -42.17 | Gas improved slightly

## March
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-03-06
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 10 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0.4 | 0.9 | 19.6 | 79.1 | 0 | 0 | 1002 | -0.35 | 1 | 8.8
BK BH 3 | 9:51 | 0.8 | 1.5 | 20.1 | 77.6 | 0 | 0 | 1002 | 0.76 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.21 | 1 | 5.1
BK BH 5 | 9:54 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | -0.36 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.9 | 20.4 | 78.7 | 0 | 0 | 1002 | 0.52 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 2.1 | 20.2 | 77.7 | 0 | 0 | 1002 | 0.48 | 1 | 10
BK BH 8 | 10:05 | 30.1 | 3.1 | 19.9 | 46.9 | 0 | 0 | 1002 | -0.15 | 32.2 | 3.6
BK BH 9 | 10:11 | 28.8 | 5.2 | 20.2 | 45.8 | 0 | 0 | 1002 | 0.36 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | -0.25 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 1002 | 0.16 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 2.7 | 20.3 | 77 | 0 | 0 | 1002 | 0.87 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 1002 | -0.11 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.35 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 3.6 | 19.9 | 76.5 | 0 | 0 | 1002 | -0.56 | 1 | 17.6
BK BH 16 | 10:45 | 0.3 | 2.5 | 19.1 | 78.1 | 0 | 0 | 1002 | 0.48 | 1 | 11.4
BK BH 17 | 10:52 | 0 | 1.6 | 20.3 | 78.1 | 0 | 0 | 1002 | -0.11 | 1 | 12.9
BK BH 18 | 9:18 | 3.2 | 2.4 | 20.1 | 74.3 | 0 | 0 | 1002 | 0.25 | 6.8 | 21.2
BK BH 19 | 9:22 | 0.7 | 1.6 | 19.5 | 78.2 | 0 | 0 | 1002 | 0.69 | 1 | 11.2
BK BH 20 | 9:25 | 0.8 | 5 | 19.1 | 75.1 | 0 | 0 | 1002 | -0.17 | 1 | 10.7
BK BH 21 | 9:30 | 0.4 | 7.1 | 15.2 | 77.3 | 0 | 0 | 1002 | 0.02 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 3.4 | 19.2 | 77.4 | 0 | 0 | 1002 | 0.39 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.9 | 20.3 | 78.8 | 0 | 0 | 1002 | -0.42 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1002 | 0.28 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-03-13
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 15 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0.3 | 1.2 | 19.8 | 78.7 | 0 | 0 | 998 | -0.54 | 1 | 8.8
BK BH 3 | 10:08 | 0.7 | 1.3 | 20.1 | 77.9 | 0 | 0 | 998 | 0.32 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 998 | -0.32 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 998 | 0.28 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.7 | 20.2 | 79.1 | 0 | 0 | 998 | 0.19 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 998 | -0.65 | 1 | 10
BK BH 8 | 10:22 | 30 | 3.2 | 19.9 | 46.9 | 0 | 0 | 998 | 0.34 | 32.2 | 3.6
BK BH 9 | 10:28 | 29 | 5 | 20.1 | 45.9 | 0 | 0 | 998 | -0.11 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.9 | 19.7 | 78.4 | 0 | 0 | 998 | 0.25 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 2.5 | 19.5 | 78 | 0 | 0 | 998 | -0.37 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 2.7 | 20.1 | 77.2 | 0 | 0 | 998 | -0.87 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 998 | 0.69 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.5 | 19.4 | 79.1 | 0 | 0 | 998 | -0.11 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 3.5 | 20.1 | 76.4 | 0 | 0 | 998 | 0.23 | 1 | 17.6
BK BH 16 | 11:02 | 0.4 | 2.3 | 19.3 | 78 | 0 | 0 | 998 | -0.42 | 1 | 11.4
BK BH 17 | 11:09 | 0.1 | 1.4 | 20.2 | 78.3 | 0 | 0 | 998 | 0.36 | 1 | 12.9
BK BH 18 | 9:35 | 3.8 | 2.9 | 20.4 | 72.9 | 0 | 0 | 998 | -0.11 | 6.8 | 21.2
BK BH 19 | 9:39 | 0.6 | 1.3 | 19.6 | 78.5 | 0 | 0 | 998 | -0.17 | 1 | 11.2
BK BH 20 | 9:42 | 0.7 | 5.3 | 19.2 | 74.8 | 0 | 0 | 998 | 0.6 | 1 | 10.7
BK BH 21 | 9:47 | 0.6 | 6.9 | 15.8 | 76.7 | 0 | 0 | 998 | 0.27 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 3.2 | 19.6 | 77.2 | 0 | 0 | 998 | -0.14 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 998 | 0.25 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 998 | -0.58 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-03-20
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 17 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-03-20
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:27 | 0.4 | 1.1 | 20 | 78.5 | 0 | 0 | 999 | -0.25 | 1 | 8.8
BK BH 3 | 10:32 | 0.6 | 1.5 | 19.9 | 78 | 0 | 0 | 999 | 0.49 | 1 | 3.1
BK BH 4 | 10:34 | 0 | 2.2 | 19.5 | 78.3 | 0 | 0 | 999 | 0.32 | 1 | 5.1
BK BH 5 | 10:36 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 999 | 0.19 | 1 | 1.5
BK BH 6 | 10:39 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | 0.25 | 1 | 1.5
BK BH 7 | 10:43 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 999 | 0.36 | 1 | 10
BK BH 8 | 10:46 | 30.2 | 2.9 | 20.1 | 46.8 | 0 | 0 | 999 | -0.01 | 32.2 | 3.6
BK BH 9 | 10:52 | 29.3 | 5.2 | 20 | 45.5 | 0 | 0 | 999 | 0.53 | 29.6 | 10.4
BK BH 10 | 10:57 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 999 | 0.24 | 1 | 3.9
BK BH 11 | 11:09 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 999 | -0.11 | 1 | 6.5
BK BH 12 | 11:13 | 0 | 2.9 | 20.3 | 76.8 | 0 | 0 | 999 | 0.56 | 1 | 6.6
BK BH 13 | 11:17 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 999 | 0.38 | 1 | 9.4
BK BH 14 | 11:20 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 999 | 0.14 | 1 | 3.5
BK BH 15 | 11:23 | 0 | 3.2 | 19 | 77.8 | 0 | 0 | 999 | 0.25 | 1 | 17.6
BK BH 16 | 11:26 | 0.5 | 1.9 | 19.5 | 78.1 | 0 | 0 | 999 | 0.36 | 1 | 11.4
BK BH 17 | 11:33 | 0.3 | 1.1 | 20.1 | 78.5 | 0 | 0 | 999 | -0.14 | 1 | 12.9
BK BH 18 | 9:59 | 3.9 | 3.2 | 20.3 | 72.6 | 0 | 0 | 999 | 0.36 | 6.8 | 21.2
BK BH 19 | 10:03 | 0.8 | 1.6 | 19.8 | 77.8 | 0 | 0 | 999 | -0.98 | 1 | 11.2
BK BH 20 | 10:06 | 0.8 | 5.5 | 19 | 74.7 | 0 | 0 | 999 | 0.75 | 1 | 10.7
BK BH 21 | 10:11 | 0.9 | 7 | 16 | 76.1 | 0 | 0 | 999 | -0.15 | 1 | 21.7
BK BH 23 | 10:16 | 0 | 3.9 | 19.9 | 76.2 | 0 | 0 | 999 | 0.36 | 1 | 7.3
BK BH 24 | 10:19 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | -0.48 | 1 | 1.5
BK BH 25 | 10:23 | 0 | 1.3 | 20.3 | 78.4 | 0 | 0 | 999 | 0.21 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-03-27
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 17 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0.3 | 1.3 | 20.3 | 78.1 | 0 | 0 | 1002 | -0.21 | 1 | 8.8
BK BH 3 | 10:08 | 0.5 | 1.2 | 20.1 | 78.2 | 0 | 0 | 1002 | 0.25 | 1 | 3.1
BK BH 4 | 10:11 | 0 | 2.5 | 19.6 | 77.9 | 0 | 0 | 1002 | 0.23 | 1 | 5.1
BK BH 5 | 10:13 | 0 | 1 | 19.1 | 79.9 | 0 | 0 | 1002 | -0.49 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.6 | 20.3 | 79.1 | 0 | 0 | 1002 | -0.56 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | 0.24 | 1 | 10
BK BH 8 | 10:22 | 30.6 | 3.3 | 20.3 | 45.8 | 0 | 0 | 1002 | -0.11 | 32.2 | 3.6
BK BH 9 | 10:28 | 28.9 | 5 | 20.2 | 45.9 | 0 | 0 | 1002 | -0.28 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | -0.63 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1002 | 0.11 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 2.8 | 20.3 | 76.9 | 0 | 0 | 1002 | 0.78 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | -0.15 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.21 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 3 | 19.6 | 77.4 | 0 | 0 | 1002 | -0.63 | 1 | 17.6
BK BH 16 | 11:02 | 0.4 | 1.6 | 19.2 | 78.8 | 0 | 0 | 1002 | 0.21 | 1 | 11.4
BK BH 17 | 11:09 | 0.2 | 1.4 | 20 | 78.4 | 0 | 0 | 1002 | -0.75 | 1 | 12.9
BK BH 18 | 9:35 | 3.6 | 3 | 20.4 | 73 | 0 | 0 | 1002 | -0.63 | 6.8 | 21.2
BK BH 19 | 9:39 | 0.6 | 1.3 | 19.6 | 78.5 | 0 | 0 | 1002 | 0.54 | 1 | 11.2
BK BH 20 | 9:42 | 0.9 | 5.2 | 19.8 | 74.1 | 0 | 0 | 1002 | -0.96 | 1 | 10.7
BK BH 21 | 9:47 | 0.9 | 7.5 | 16.5 | 75.1 | 0 | 0 | 1002 | -0.12 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 3.2 | 19.6 | 77.2 | 0 | 0 | 1002 | 0.34 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 1 | 20.3 | 78.7 | 0 | 0 | 1002 | -0.44 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | 0.25 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-03-12
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 14 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-03-20
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:50 | 39.6 | 3.6 | 3.6 | 23.8 | 2 | 0 | 998 | -40.25
GV1 |  | 57.4 | 40.2 | 0 | 32.3 | 4 | 0 | 998 | -8.95 | Reg opened full
GV2 |  | 61.2 | 39.1 | 0 | 35.6 | 5 | 0 | 998 | -4.58 | reg opened full
GV3 |  | 64.7 | 37.9 | 0.1 | 13.2 | 3 | 0 | 998 | -24.78 | Left Open Full
GV4 |  | 64.4 | 37.4 | 0.1 | 24.1 | 4 | 0 | 998 | -25.89 | Reg opened full
GV5+R1 |  | 61.1 | 40.7 | 0.1 | 11.8 | 3 | 0 | 998 | -35.21 | Left Open full
GV6 |  | 57.8 | 42.1 | 0.1 | 9.4 | 4 | 0 | 998 | -30.02 | Left Open Full
GV7 |  | 42.8 | 32.4 | 0.9 | 17 | 6 | 0 | 998 | -12.36 | Left Cracked Open
GV8 |  | 41.1 | 32.1 | 2 | 25.7 | 4 | 0 | 998 | -14 | reg closed too cracked open
GV9 |  | 59.3 | 39.8 | 0.2 | 16 | 4 | 0 | 998 | -25.69 | Left Open Full
GV9.1 |  | 54 | 37.7 | 0.9 | 46.9 | 5 | 0 | 998 | -2.02 | reg opened full
GV10 |  | 44.9 | 32.2 | 4.7 | 39.1 | 4 | 0 | 998 | 1.58 | Left closed
GV11 |  | 40.1 | 30.4 | 5.7 | 19.7 | 4 | 0 | 998 | 1.69 | reg closed bad gas
GV12+R3 |  | 55 | 41.9 | 0.9 | 14.9 | 8 | 0 | 998 | -25.69 | Left Open Full
GV13 |  | 31.6 | 25.1 | 8.9 | 74.4 | 5 | 0 | 998 | 1.02 | Left Off
GV14 |  | 60.5 | 41.3 | 0.2 | 17.5 | 6 | 0 | 998 | -26.87 | Left Open Full
GV15 |  | 57.3 | 42.1 | 0.1 | 17 | 7 | 0 | 998 | -12.39 | Left Open Full
GV16 |  | 60.4 | 40.8 | 0.2 | 16.9 | 6 | 0 | 998 | -14.58 | Left open full
GV17+LC4 |  | 5.1 | 4.3 | 18.1 | 11.9 | 0 | 0 | 998 | 2.36 | Reg turned off
GV18+21 |  | 58.9 | 42.1 | 0.1 | 14.8 | 5 | 0 | 998 | -17.89 | Left open full
GV19 |  | 17.5 | 18.5 | 5.5 | 42.2 | 0 | 0 | 998 | 1.58 | Left Off
GV20 |  | 0 | 2.8 | 19.6 | 82 | 0 | 0 | 998 | 0.87 | Left Off
GV 22 + CVs |  | 58.1 | 45.8 | 0.2 | 17.2 | 6 | 0 | 998 | -29.63 | Left Open Full
GV23 |  | 58 | 43.8 | 0 | 14.1 | 6 | 0 | 998 | -32.14 | Left Open Full
GV24 |  | 58 | 43.2 | 0 | 10.9 | 6 | 0 | 998 | -12.38 | Left Open Full
GV25 |  | 58.9 | 42.2 | 0.1 | 13.7 | 4 | 0 | 998 | -14.32 | Left Open Full
GV26/A |  | 57 | 40.4 | 0.3 | 18.5 | 4 | 0 | 998 | -35.89 | Left Open Full
GV27+28 / B+C |  | 58.7 | 43.1 | 0.1 | 15.6 | 7 | 0 | 998 | -24.88 | left open full
GV30 |  | 54.9 | 38.7 | 0.9 | 36 | 4 | 0 | 998 | -12.45 | reg opened full
GV31 |  | 52.6 | 37.6 | 1.6 | 16.4 | 5 | 0 | 998 | -12.36 | Reg closed too half way
GV32 |  | 58.4 | 43.9 | 0.2 | 16.8 | 7 | 0 | 998 | -15.77 | Left open full
GV33 |  | 53.4 | 37.9 | 1.7 | 25.9 | 6 | 0 | 998 | -12.47 | Reg opened too half way
GV34 |  | 51.3 | 37 | 0.4 | 13.5 | 1 | 0 | 998 | -17.22 | Left open full
RP6.1 |  | 0.4 | 6.7 | 20.1 | 64.8 | 4 | 0 | 998 | 0.78 | Left Off
Point: LC1B |  | Off at the minute pump getting fixed.
LC1.1 |  | 27.1 | 20.2 | 5.9 | 58.6 | 5 | 0 | 998 | 1.23 | Left Off
LC2R? |  | 42.5 | 31.6 | 1.6 | 44.4 | 4 | 0 | 998 | -13.55 | reg cracked open
GV 2.1 |  | 58.2 | 43.2 | 0 | 12.1 | 8 | 0 | 998 | -15.47 | Left Open Full
GV 2.2+ LC2B |  | 59.7 | 39.7 | 0.1 | 31.8 | 4 | 0 | 998 | -11.22 | Left Open full
GV / LC3.1 + LC3 |  | 29.6 | 23.4 | 9.3 | 25.8 | 4 | 0 | 998 | 1.24 | Reg turned off
LC4B |  | 59.4 | 47.4 | 0.1 | 17 | 5 | 0 | 998 | -21.79 | Left open full
LC5 |  | 22.1 | 16.8 | 13.1 | 17.4 | 2 | 0 | 998 | 2.06 | Left off
LC6 |  | 34.9 | 28.1 | 7 | 20.8 | 1 | 0 | 998 | 1.34 | Left off
GV29D + LC6B |  | 59 | 43 | 0.1 | 19.5 | 7 | 0 | 998 | -25.98 | Left Open Full
PW1 |  | 35.2 | 15.2 | 5 | 40.6 | 9 | 48 | 998 | 1.98 | Left Off bad gas high o2
PW2 |  | 50.8 | 32.6 | 1.1 | 15 | 12 | 89 | 998 | -13.74 | left Cracked Open
PW3 |  | 14.6 | 12.1 | 9.9 | 62.6 | 7 | 3 | 998 | 2.14 | Well Left Off
PW4 |  | 30.2 | 20.2 | 4.1 | 40.4 | 8 | 4 | 998 | 1.06 | left off
PW5 |  | 25.9 | 23.4 | 2.8 | 43.4 | 9 | 9 | 998 | 0.69 | left off
PW6 |  | 50.9 | 30.1 | 0.4 | 18.6 | 12 | 12 | 998 | -22.1 | Left Opened Full
Cap Vent |  | 48.7 | 32.6 | 2.9 | 18.3 | 7 | 8 | 998 | 0.58 | left off
Flare | 15:05 | 52.1 | 33.2 | 1.5 | 20.1 | 16 | 12 | 998 | -45.69 | Gas improved a lot. Engine 560

## April
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-04-03
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0.2 | 1.6 | 20.1 | 78.1 | 0 | 0 | 999 | -0.35 | 1 | 8.8
BK BH 3 | 9:51 | 0.4 | 1.1 | 19.9 | 78.6 | 0 | 0 | 999 | 0.76 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 999 | 0.45 | 1 | 5.1
BK BH 5 | 9:54 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 999 | -0.02 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | 0.52 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 2.5 | 19.6 | 77.9 | 0 | 0 | 999 | 0.48 | 1 | 10
BK BH 8 | 10:05 | 30.1 | 3 | 20.3 | 46.6 | 0 | 0 | 999 | -0.15 | 32.2 | 3.6
BK BH 9 | 10:11 | 28.5 | 5.2 | 20 | 46.3 | 0 | 0 | 999 | 0.36 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 999 | -0.25 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.1 | 19.2 | 78.7 | 0 | 0 | 999 | 0.16 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 2.2 | 19.9 | 77.9 | 0 | 0 | 999 | 0.87 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 999 | -0.11 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.1 | 20.4 | 78.5 | 0 | 0 | 999 | 0.35 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 2.8 | 19.6 | 77.6 | 0 | 0 | 999 | -0.56 | 1 | 17.6
BK BH 16 | 10:45 | 0.3 | 1.4 | 19.5 | 78.8 | 0 | 0 | 999 | 0.48 | 1 | 11.4
BK BH 17 | 10:52 | 0.1 | 1.1 | 19.8 | 79 | 0 | 0 | 999 | -0.11 | 1 | 12.9
BK BH 18 | 9:18 | 3.2 | 2.8 | 20.3 | 73.7 | 0 | 0 | 999 | 0.25 | 6.8 | 21.2
BK BH 19 | 9:22 | 0.2 | 1.8 | 19.1 | 78.9 | 0 | 0 | 999 | 0.69 | 1 | 11.2
BK BH 20 | 9:25 | 0.8 | 5 | 19.3 | 74.9 | 0 | 0 | 999 | -0.17 | 1 | 10.7
BK BH 21 | 9:30 | 0.7 | 7.2 | 16.8 | 75.3 | 0 | 0 | 999 | 0.02 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 3 | 19 | 78 | 0 | 0 | 999 | 0.39 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 1.1 | 20.6 | 78.3 | 0 | 0 | 999 | -0.42 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.4 | 20.4 | 78.2 | 0 | 0 | 999 | 0.28 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-04-10
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0.3 | 1.9 | 20.3 | 77.5 | 0 | 0 | 995 | -0.52 | 1 | 8.8
BK BH 3 | 10:08 | 0.6 | 1.5 | 19.5 | 78.4 | 0 | 0 | 995 | -0.12 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 995 | -0.19 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 995 | 0.23 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 995 | 0.77 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 995 | 0.52 | 1 | 10
BK BH 8 | 10:22 | 30.9 | 2.8 | 20.1 | 46.2 | 0 | 0 | 995 | 0.46 | 32.2 | 3.6
BK BH 9 | 10:28 | 29 | 5.9 | 19.4 | 45.7 | 0 | 0 | 995 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 995 | 0.36 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 995 | -0.25 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 2 | 20.1 | 77.9 | 0 | 0 | 995 | -0.11 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.8 | 20.4 | 77.8 | 0 | 0 | 995 | 0.69 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 995 | 0.75 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 2.3 | 19.2 | 78.5 | 0 | 0 | 995 | -0.11 | 1 | 17.6
BK BH 16 | 11:02 | 0.2 | 1.6 | 19.6 | 78.6 | 0 | 0 | 995 | 0.29 | 1 | 11.4
BK BH 17 | 11:09 | 0.4 | 1.4 | 20.3 | 77.9 | 0 | 0 | 995 | -0.26 | 1 | 12.9
BK BH 18 | 9:35 | 3.5 | 2.9 | 20.5 | 73.1 | 0 | 0 | 995 | 0.52 | 6.8 | 21.2
BK BH 19 | 9:39 | 0.4 | 1.4 | 19 | 79.2 | 0 | 0 | 995 | 0.46 | 1 | 11.2
BK BH 20 | 9:42 | 0.5 | 5.2 | 19.6 | 74.7 | 0 | 0 | 995 | -0.68 | 1 | 10.7
BK BH 21 | 9:47 | 0.4 | 7 | 17.4 | 75.2 | 0 | 0 | 995 | -0.08 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 3.9 | 19.5 | 76.6 | 0 | 0 | 995 | 0.21 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 1 | 20.2 | 78.8 | 0 | 0 | 995 | -0.42 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.2 | 20.7 | 78.1 | 0 | 0 | 995 | 0.38 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-04-17
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0.4 | 1.4 | 20.3 | 77.9 | 0 | 0 | 996 | -0.54 | 1 | 8.8
BK BH 3 | 10:28 | 0.5 | 1 | 19.6 | 78.9 | 0 | 0 | 996 | 0.38 | 1 | 3.1
BK BH 4 | 10:29 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 996 | 0.48 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 996 | -0.58 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 996 | 0.21 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 996 | 0.36 | 1 | 10
BK BH 8 | 10:42 | 30.5 | 2.5 | 20.4 | 46.6 | 0 | 0 | 996 | 0.58 | 32.2 | 3.6
BK BH 9 | 10:48 | 28.1 | 5.7 | 19.1 | 47.1 | 0 | 0 | 996 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 996 | 0.68 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 2 | 19.1 | 78.9 | 0 | 0 | 996 | 0.87 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 2.3 | 19 | 78.7 | 0 | 0 | 996 | 0.59 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 1 | 20.3 | 78.7 | 0 | 0 | 996 | 0.23 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 996 | 0.87 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 2.6 | 19.5 | 77.9 | 0 | 0 | 996 | -0.15 | 1 | 17.6
BK BH 16 | 11:22 | 0.3 | 1.9 | 19 | 78.8 | 0 | 0 | 996 | 0.23 | 1 | 11.4
BK BH 17 | 11:29 | 0.6 | 1.1 | 19.9 | 78.4 | 0 | 0 | 996 | -0.46 | 1 | 12.9
BK BH 18 | 9:55 | 3.1 | 2.5 | 20.3 | 74.1 | 0 | 0 | 996 | 0.68 | 6.8 | 21.2
BK BH 19 | 9:59 | 0.5 | 1.1 | 18.9 | 79.5 | 0 | 0 | 996 | 0.78 | 1 | 11.2
BK BH 20 | 10:02 | 0.4 | 5.6 | 19.9 | 74.1 | 0 | 0 | 996 | -0.15 | 1 | 10.7
BK BH 21 | 10:07 | 0.5 | 9.1 | 18.1 | 72.3 | 0 | 0 | 996 | 0.24 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 3.5 | 19.2 | 77.3 | 0 | 0 | 996 | 0.25 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 996 | -0.78 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.1 | 20.4 | 78.5 | 0 | 0 | 996 | 0.52 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-04-24
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 17 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0.3 | 1.1 | 20.1 | 78.5 | 0 | 0 | 1002 | -0.96 | 1 | 8.8
BK BH 3 | 10:24 | 0.4 | 1.1 | 19.5 | 79 | 0 | 0 | 1002 | 0.36 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 1002 | -0.74 | 1 | 5.1
BK BH 5 | 10:27 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 1002 | 0.23 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 0.5 | 19.1 | 80.4 | 0 | 0 | 1002 | 0.87 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 2.4 | 20.1 | 77.5 | 0 | 0 | 1002 | 0.53 | 1 | 10
BK BH 8 | 10:38 | 30.4 | 2.5 | 20.3 | 46.8 | 0 | 0 | 1002 | 0.26 | 32.2 | 3.6
BK BH 9 | 10:44 | 27.4 | 5.2 | 19.5 | 47.9 | 0 | 0 | 1002 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 1002 | 0.75 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 2.5 | 19.4 | 78.1 | 0 | 0 | 1002 | 0.21 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 2.1 | 18.6 | 79.3 | 0 | 0 | 1002 | -0.44 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 1002 | 0.63 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 1002 | 0.24 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 2.4 | 19.2 | 78.4 | 0 | 0 | 1002 | -0.16 | 1 | 17.6
BK BH 16 | 11:18 | 0.4 | 1.9 | 19.8 | 77.9 | 0 | 0 | 1002 | 0.94 | 1 | 11.4
BK BH 17 | 11:25 | 0.8 | 1 | 20.3 | 77.9 | 0 | 0 | 1002 | 0.87 | 1 | 12.9
BK BH 18 | 9:51 | 3 | 2.6 | 20.3 | 74.1 | 0 | 0 | 1002 | -0.12 | 6.8 | 21.2
BK BH 19 | 9:55 | 0.6 | 1.1 | 19.6 | 78.7 | 0 | 0 | 1002 | 0.35 | 1 | 11.2
BK BH 20 | 9:58 | 0.2 | 5.1 | 20 | 74.7 | 0 | 0 | 1002 | -0.78 | 1 | 10.7
BK BH 21 | 10:03 | 0.1 | 9.4 | 19.6 | 70.9 | 0 | 0 | 1002 | 0.63 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 3.2 | 19.5 | 77.3 | 0 | 0 | 1002 | 0.25 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 0.8 | 20.4 | 78.8 | 0 | 0 | 1002 | -0.14 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 1.1 | 20.7 | 78.2 | 0 | 0 | 1002 | 0.71 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-04-26
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 13 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:30 | 43.8 | 4.2 | 2.1 | 49.9 | 0 | 0 | 999 | -37.28
GV1 |  | 52.1 | 38.7 | 1.1 | 8.1 | 0 | 0 | 999 | -9 | Reg closed too half way o2 creeped up
GV2 |  | 60.2 | 38 | 0.2 | 1.6 | 0 | 0 | 999 | -5.23 | Left Open full
GV3 |  | 59.9 | 35.7 | 0.4 | 4 | 0 | 0 | 999 | -22.47 | Left Open Full
GV4 |  | 58.4 | 33.2 | 0.5 | 7.9 | 0 | 0 | 999 | -24.69 | Left Open full
GV5+R1 |  | 57.7 | 41.2 | 0.03 | 1.07 | 0 | 0 | 999 | -33.98 | Left Open full
GV6 |  | 55.2 | 42.1 | 0.1 | 2.6 | 0 | 0 | 999 | -31.25 | Left Open Full
GV7 |  | 44.5 | 30.2 | 1.1 | 24.2 | 0 | 0 | 999 | -13.04 | Left Cracked Open
GV8 |  | 45.2 | 30.2 | 1 | 23.6 | 0 | 0 | 999 | -11.47 | left cracked open
GV9 |  | 55.4 | 35.1 | 0.4 | 9.1 | 0 | 0 | 999 | -26 | Left Open Full
GV9.1 |  | 50.2 | 35.1 | 0.7 | 14 | 0 | 0 | 999 | -2.08 | left open full
GV10 |  | 42.1 | 30.2 | 4.1 | 23.6 | 0 | 0 | 999 | 1.23 | Left closed
GV11 |  | 40.5 | 30.9 | 5.1 | 23.5 | 0 | 0 | 999 | 1.47 | Left Off
GV12+R3 |  | 54.2 | 40.7 | 0.7 | 4.4 | 0 | 0 | 999 | -24.51 | Left Open Full
GV13 |  | 33.2 | 25.9 | 8 | 32.9 | 0 | 0 | 999 | 1.08 | Left Off
GV14 |  | 59.7 | 31.8 | 0.3 | 8.2 | 0 | 4 | 999 | -26.99 | Left Open Full
GV15 |  | 55.1 | 39.7 | 0.5 | 4.7 | 0 | 1 | 999 | -14.27 | Left Open Full
GV16 |  | 59.8 | 35.6 | 0.1 | 4.5 | 0 | 0 | 999 | -14.44 | Left open full
GV17+LC4 |  | 4.8 | 5.2 | 17.7 | 72.3 | 0 | 0 | 999 | 2.01 | left off
GV18+21 |  | 55.6 | 40 | 0.3 | 4.1 | 0 | 0 | 999 | -19.98 | Left open full
GV19 |  | 19.9 | 19 | 5.4 | 55.7 | 0 | 0 | 999 | 1 | Left Off
GV20 |  | 0.1 | 2.8 | 18.6 | 78.5 | 0 | 0 | 999 | 0.21 | Left Off
GV 22 + CVs |  | 56 | 42.1 | 0.3 | 1.6 | 0 | 0 | 999 | -28.97 | Left Open Full
GV23 |  | 55.6 | 40.2 | 0.2 | 4 | 0 | 0 | 999 | -30.63 | Left Open Full
GV24 |  | 57.4 | 33.9 | 0.1 | 8.6 | 0 | 0 | 999 | -13.22 | Left Open Full
GV25 |  | 59.2 | 39.9 | 0.5 | 0.4 | 0 | 0 | 999 | -12.78 | Left Open Full
GV26/A |  | 54.7 | 40 | 0.8 | 4.5 | 0 | 0 | 999 | -38.99 | Left Open Full
GV27+28 / B+C |  | 55.6 | 40.2 | 0.4 | 3.8 | 0 | 0 | 999 | -21.47 | left open full
GV30 |  | 50.2 | 33.6 | 0.5 | 15.7 | 0 | 0 | 999 | -13.32 | Left open full
GV31 |  | 50.1 | 33.5 | 1.1 | 15.3 | 0 | 0 | 999 | -13.88 | Reg closed too cracked
GV32 |  | 55.6 | 43 | 0.3 | 1.1 | 0 | 0 | 999 | -15.27 | Left open full
GV33 |  | 40 | 35.8 | 1.2 | 23 | 0 | 0 | 999 | -13.36 | Reg closed bad gas
GV34 |  | 55.8 | 33.2 | 0.3 | 10.7 | 0 | 0 | 999 | -20.36 | Left open full
RP6.1 |  | 0.5 | 5 | 19.6 | 74.9 | 0 | 0 | 999 | 0.58 | Left Off
LC1B |  | 0.2 | 0.3 | 18.9 | 80.6 | 0 | 0 | 999 | -3.87 | Left Off
LC1.1 |  | 22.1 | 19.6 | 6.3 | 52 | 0 | 0 | 999 | 1.02 | Left Off
LC2R? |  | 44.5 | 30.6 | 1 | 23.9 | 0 | 0 | 999 | -15.69 | Left cracked Open
GV 2.1 |  | 56.7 | 39.6 | 0.2 | 3.5 | 0 | 0 | 999 | -17.12 | Left Open Full
GV 2.2+ LC2B |  | 54.2 | 35.6 | 0.4 | 9.8 | 0 | 0 | 999 | -12.39 | Left Open full
GV / LC3.1 + LC3 |  | 30 | 25.1 | 8.7 | 36.2 | 0 | 0 | 999 | 1.21 | left turned off
LC4B |  | 55.1 | 44.1 | 0.3 | 0.5 | 0 | 0 | 999 | -20.39 | Left open full
LC5 |  | 20.3 | 17.9 | 12.1 | 49.7 | 0 | 0 | 999 | 2.08 | Left off
LC6 |  | 32.8 | 25.6 | 7.8 | 33.8 | 0 | 0 | 999 | 1.24 | Left off
GV29D + LC6B |  | 58.9 | 40 | 0.2 | 0.9 | 0 | 0 | 999 | -28.91 | Left Open Full
PW1 |  | 36.9 | 14.5 | 4.8 | 43.8 | 0 | 0 | 999 | 1 | Left Off bad gas high o2
PW2 |  | 50.1 | 33.9 | 1.2 | 14.8 | 0 | 0 | 999 | -10.24 | Left cracked open
PW3 |  | 13.6 | 15 | 9.1 | 62.3 | 0 | 0 | 999 | 2.56 | Well Left Off
PW4 |  | 31.2 | 19.8 | 4.8 | 44.2 | 0 | 0 | 999 | 1.09 | left off
PW5 |  | 26.9 | 25 | 2.9 | 45.2 | 0 | 0 | 999 | 0.54 | left off
PW6 |  | 52.3 | 29.6 | 0.5 | 17.6 | 0 | 1 | 999 | -22.99 | Left Opened Full
Point: Cap Vent; mb: 999 |  | Not connected.
Flare | 15:00 | 49.8 | 27.9 | 1.2 | 21.1 | 0 | 0 | 999 | -39.32 | Gas improved a lot. Engine 560

## May
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-05-01
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 18 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:42 | 0.2 | 1.2 | 19.9 | 78.7 | 0 | 0 | 999 | 0.89 | 1 | 8.8
BK BH 3 | 10:47 | 0.3 | 1.6 | 19.8 | 78.3 | 0 | 0 | 999 | -0.64 | 1 | 3.1
BK BH 4 | 10:49 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.52 | 1 | 5.1
BK BH 5 | 10:52 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 999 | 0.78 | 1 | 1.5
BK BH 6 | 10:54 | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 999 | 0.68 | 1 | 1.5
BK BH 7 | 10:58 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 999 | 0.89 | 1 | 10
BK BH 8 | 11:01 | 30.1 | 2.1 | 20.4 | 47.4 | 0 | 0 | 999 | 0.78 | 32.2 | 3.6
BK BH 9 | 11:07 | 27.1 | 5 | 19.6 | 48.3 | 0 | 0 | 999 | 0.88 | 29.6 | 10.4
BK BH 10 | 11:12 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | 0.98 | 1 | 3.9
BK BH 11 | 11:14 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 999 | -0.85 | 1 | 6.5
BK BH 12 | 11:28 | 0 | 1.8 | 18.7 | 79.5 | 0 | 0 | 999 | 0.58 | 1 | 6.6
BK BH 13 | 11:22 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 999 | -0.88 | 1 | 9.4
BK BH 14 | 11:35 | 0 | 1 | 19.2 | 79.8 | 0 | 0 | 999 | 0.62 | 1 | 3.5
BK BH 15 | 11:38 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 999 | 0.84 | 1 | 17.6
BK BH 16 | 11:41 | 0.5 | 1.5 | 20 | 78 | 0 | 0 | 999 | 1.02 | 1 | 11.4
BK BH 17 | 11:48 | 0.7 | 1.2 | 20.2 | 77.9 | 0 | 0 | 999 | 0.91 | 1 | 12.9
BK BH 18 | 10:14 | 2.7 | 2.8 | 20.4 | 74.1 | 0 | 0 | 999 | 0.63 | 6.8 | 21.2
BK BH 19 | 10:18 | 0.5 | 1.3 | 19.5 | 78.7 | 0 | 0 | 999 | 0.9 | 1 | 11.2
BK BH 20 | 10:21 | 0.4 | 4.9 | 19.6 | 75.1 | 0 | 0 | 999 | 0.87 | 1 | 10.7
BK BH 21 | 10:26 | 0.2 | 9.1 | 19.8 | 70.9 | 0 | 0 | 999 | 0.72 | 1 | 21.7
BK BH 23 | 10:31 | 0 | 3 | 19.2 | 77.8 | 0 | 0 | 999 | 0.82 | 1 | 7.3
BK BH 24 | 10:34 | 0 | 0.7 | 20.3 | 79 | 0 | 0 | 999 | -0.48 | 1 | 1.5
BK BH 25 | 10:38 | 0 | 1.2 | 20.5 | 78.3 | 0 | 0 | 999 | 0.93 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-05-08
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0.3 | 1.3 | 19.8 | 78.6 | 0 | 0 | 1009 | 0.79 | 1 | 8.8
BK BH 3 | 10:24 | 0.2 | 1.2 | 19.6 | 79 | 0 | 0 | 1009 | -0.69 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1009 | 0.89 | 1 | 5.1
BK BH 5 | 10:28 | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 1009 | -0.23 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 1009 | 0.72 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1009 | 0.94 | 1 | 10
BK BH 8 | 10:38 | 29.9 | 2 | 20.3 | 47.8 | 0 | 0 | 1009 | 0.71 | 32.2 | 3.6
BK BH 9 | 10:44 | 27.5 | 4.9 | 19.8 | 47.8 | 0 | 0 | 1009 | 0.9 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 1009 | 0.87 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 2.1 | 19.2 | 78.7 | 0 | 0 | 1009 | -0.88 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 1.6 | 18.9 | 79.5 | 0 | 0 | 1009 | 0.62 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 1009 | -0.97 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1009 | 0.56 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 2.4 | 20.1 | 77.5 | 0 | 0 | 1009 | 0.74 | 1 | 17.6
BK BH 16 | 11:18 | 0.4 | 1.3 | 19.9 | 78.4 | 0 | 0 | 1009 | 1.13 | 1 | 11.4
BK BH 17 | 11:25 | 0.5 | 1.5 | 20.4 | 77.6 | 0 | 0 | 1009 | 0.99 | 1 | 12.9
BK BH 18 | 9:51 | 2.5 | 2.4 | 20.1 | 75 | 0 | 0 | 1009 | 0.68 | 6.8 | 21.2
BK BH 19 | 9:55 | 0.4 | 1 | 19.6 | 79 | 0 | 0 | 1009 | 0.81 | 1 | 11.2
BK BH 20 | 9:58 | 0.5 | 5.2 | 19.4 | 74.9 | 0 | 0 | 1009 | 0.57 | 1 | 10.7
BK BH 21 | 10:03 | 0.3 | 9 | 19.4 | 71.3 | 0 | 0 | 1009 | 0.89 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 2.9 | 19.3 | 77.8 | 0 | 0 | 1009 | 0.34 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1009 | -0.58 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 1.4 | 20.6 | 78 | 0 | 0 | 1009 | 0.87 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-05-15
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:02 | 0.5 | 1.1 | 19.6 | 78.8 | 0 | 0 | 1005 | 0.69 | 1 | 8.8
BK BH 3 | 10:07 | 0.3 | 1.4 | 19.2 | 79.1 | 0 | 0 | 1005 | -0.48 | 1 | 3.1
BK BH 4 | 10:09 | 0 | 1.3 | 20.2 | 78.5 | 0 | 0 | 1005 | -0.23 | 1 | 5.1
BK BH 5 | 10:11 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1005 | 0.87 | 1 | 1.5
BK BH 6 | 10:14 | 0 | 0.6 | 19.1 | 80.3 | 0 | 0 | 1005 | 0.72 | 1 | 1.5
BK BH 7 | 10:18 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 1005 | 0.87 | 1 | 10
BK BH 8 | 10:21 | 30.2 | 1.5 | 20.1 | 48.2 | 0 | 0 | 1005 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:27 | 27.9 | 5.2 | 19.9 | 47 | 0 | 0 | 1005 | 0.78 | 29.6 | 10.4
BK BH 10 | 10:32 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1005 | 0.71 | 1 | 3.9
BK BH 11 | 10:34 | 0 | 2.4 | 19.5 | 78.1 | 0 | 0 | 1005 | -0.62 | 1 | 6.5
BK BH 12 | 10:48 | 0 | 1.6 | 19.1 | 79.3 | 0 | 0 | 1005 | 0.47 | 1 | 6.6
BK BH 13 | 10:42 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1005 | -0.97 | 1 | 9.4
BK BH 14 | 10:55 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1005 | 0.48 | 1 | 3.5
BK BH 15 | 10:58 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 1005 | 0.56 | 1 | 17.6
BK BH 16 | 11:01 | 0.3 | 1.9 | 20.3 | 77.5 | 0 | 0 | 1005 | 1.27 | 1 | 11.4
BK BH 17 | 11:08 | 0.6 | 1.1 | 20.1 | 78.2 | 0 | 0 | 1005 | 0.89 | 1 | 12.9
BK BH 18 | 9:34 | 2.1 | 2.8 | 20 | 75.1 | 0 | 0 | 1005 | 0.59 | 6.8 | 21.2
BK BH 19 | 9:38 | 0.3 | 1.5 | 19.4 | 78.8 | 0 | 0 | 1005 | 0.74 | 1 | 11.2
BK BH 20 | 9:41 | 0.4 | 5.6 | 19.6 | 74.4 | 0 | 0 | 1005 | 0.5 | 1 | 10.7
BK BH 21 | 9:46 | 0.1 | 9.2 | 19.9 | 70.8 | 0 | 0 | 1005 | 0.56 | 1 | 21.7
BK BH 23 | 9:51 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 1005 | 0.85 | 1 | 7.3
BK BH 24 | 9:54 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 1005 | -0.89 | 1 | 1.5
BK BH 25 | 9:58 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1005 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-05-22
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:41 | 0.4 | 0.9 | 19.9 | 78.8 | 0 | 0 | 1002 | -0.62 | 1 | 8.8
BK BH 3 | 9:46 | 0.6 | 1.6 | 19.5 | 78.3 | 0 | 0 | 1002 | 0.35 | 1 | 3.1
BK BH 4 | 9:48 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | -0.41 | 1 | 5.1
BK BH 5 | 9:51 | 0 | 0.4 | 19.8 | 79.8 | 0 | 0 | 1002 | 0.58 | 1 | 1.5
BK BH 6 | 9:53 | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 1002 | -0.11 | 1 | 1.5
BK BH 7 | 9:57 | 0 | 2.8 | 20.1 | 77.1 | 0 | 0 | 1002 | 0.42 | 1 | 10
BK BH 8 | 10:00 | 30.5 | 1.4 | 20.4 | 47.7 | 0 | 0 | 1002 | 0.75 | 32.2 | 3.6
BK BH 9 | 10:06 | 27.1 | 5.5 | 20.5 | 46.9 | 0 | 0 | 1002 | -0.62 | 29.6 | 10.4
BK BH 10 | 10:11 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1002 | 0.31 | 1 | 3.9
BK BH 11 | 10:23 | 0 | 2.1 | 19.4 | 78.5 | 0 | 0 | 1002 | 0.25 | 1 | 6.5
BK BH 12 | 10:27 | 0 | 1.9 | 19.2 | 78.9 | 0 | 0 | 1002 | -0.98 | 1 | 6.6
BK BH 13 | 10:31 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | 0.62 | 1 | 9.4
BK BH 14 | 10:34 | 0 | 1.6 | 20.3 | 78.1 | 0 | 0 | 1002 | 0.34 | 1 | 3.5
BK BH 15 | 10:37 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 1002 | -0.11 | 1 | 17.6
BK BH 16 | 10:40 | 0.4 | 1.4 | 20.1 | 78.1 | 0 | 0 | 1002 | 0.24 | 1 | 11.4
BK BH 17 | 10:47 | 0.6 | 0.9 | 19.7 | 78.8 | 0 | 0 | 1002 | 0.15 | 1 | 12.9
BK BH 18 | 9:13 | 2.8 | 2.9 | 20.3 | 74 | 0 | 0 | 1002 | 0.63 | 6.8 | 21.2
BK BH 19 | 9:17 | 0.6 | 1.1 | 19.6 | 78.7 | 0 | 0 | 1002 | -0.75 | 1 | 11.2
BK BH 20 | 9:20 | 0.5 | 5 | 19.8 | 74.7 | 0 | 0 | 1002 | 0.63 | 1 | 10.7
BK BH 21 | 9:25 | 0.2 | 9.5 | 20.1 | 70.2 | 0 | 0 | 1002 | 0.28 | 1 | 21.7
BK BH 23 | 9:30 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | -0.78 | 1 | 7.3
BK BH 24 | 9:33 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 1002 | 0.12 | 1 | 1.5
BK BH 25 | 9:37 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.35 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-05-28
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 20 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:38 | 0.3 | 0.8 | 20 | 78.9 | 0 | 0 | 997 | -0.52 | 1 | 8.8
BK BH 3 | 11:43 | 0.5 | 1.4 | 19.9 | 78.2 | 0 | 0 | 997 | -0.12 | 1 | 3.1
BK BH 4 | 11:45 | 0 | 1.9 | 19.4 | 78.7 | 0 | 0 | 997 | 0.45 | 1 | 5.1
BK BH 5 | 11:48 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 997 | -0.23 | 1 | 1.5
BK BH 6 | 11:50 | 0 | 0.7 | 19.4 | 79.9 | 0 | 0 | 997 | 0.77 | 1 | 1.5
BK BH 7 | 11:54 | 0 | 2.9 | 20.3 | 76.8 | 0 | 0 | 997 | 0.52 | 1 | 10
BK BH 8 | 11:57 | 30.4 | 1.1 | 20.1 | 48.4 | 0 | 0 | 997 | 0.46 | 32.2 | 3.6
BK BH 9 | 12:03 | 27.4 | 5.1 | 20 | 47.5 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4
BK BH 10 | 12:08 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 997 | 0.36 | 1 | 3.9
BK BH 11 | 12:20 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 997 | -0.25 | 1 | 6.5
BK BH 12 | 12:24 | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 997 | -0.11 | 1 | 6.6
BK BH 13 | 12:28 | 0 | 1.9 | 20.3 | 77.8 | 0 | 0 | 997 | 0.69 | 1 | 9.4
BK BH 14 | 12:31 | 0 | 1.2 | 20.5 | 78.3 | 0 | 0 | 997 | 0.75 | 1 | 3.5
BK BH 15 | 12:34 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | -0.11 | 1 | 17.6
BK BH 16 | 12:37 | 0.3 | 1.5 | 20.4 | 77.8 | 0 | 0 | 997 | 0.29 | 1 | 11.4
BK BH 17 | 12:44 | 0.5 | 0.4 | 19.5 | 79.6 | 0 | 0 | 997 | -0.26 | 1 | 12.9
BK BH 18 | 11:10 | 2.1 | 2.7 | 20.4 | 74.8 | 0 | 0 | 997 | 0.52 | 6.8 | 21.2
BK BH 19 | 11:14 | 0.9 | 1.4 | 19.8 | 77.9 | 0 | 0 | 997 | 0.46 | 1 | 11.2
BK BH 20 | 11:17 | 0.4 | 5.1 | 19.6 | 74.9 | 0 | 0 | 997 | -0.68 | 1 | 10.7
BK BH 21 | 11:22 | 0.3 | 9.2 | 20.3 | 70.2 | 0 | 0 | 997 | -0.08 | 1 | 21.7
BK BH 23 | 11:27 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 997 | 0.21 | 1 | 7.3
BK BH 24 | 11:30 | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 997 | -0.42 | 1 | 1.5
BK BH 25 | 11:34 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.38 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-05-09
Weather: |  | Wet/Raining
Wind conditions: |  | Calm
Air Temperature: |  | 14 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | RY
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:30 | 48.2 | 36.2 | 1.4 | 14.2 | 0 | 0 | 989 | -35.65
GV1 |  | 40 | 30.1 | 1 | 28.9 | 0 | 0 | 989 | -10.24 | reg closed too cracked
GV2 |  | 50.2 | 35.8 | 0.3 | 13.7 | 0 | 0 | 989 | -5.98 | Left Open full
GV3 |  | 55.9 | 33.2 | 0.1 | 10.8 | 0 | 0 | 989 | -20.14 | Left Open Full
GV4 |  | 52.6 | 38.6 | 1.1 | 7.7 | 0 | 0 | 989 | -19.89 | Reg closed too cracked
GV5+R1 |  | 52.2 | 35.3 | 1 | 11.5 | 0 | 0 | 989 | -31.27 | reg closed too cracked
GV6 |  | 54.4 | 40.1 | 0.3 | 5.2 | 0 | 0 | 989 | -30.69 | Left Open full
GV7 |  | 43.2 | 32.5 | 0.9 | 23.4 | 0 | 0 | 989 | -14.25 | Left Cracked Open
GV8 |  | 46.9 | 31.2 | 1.2 | 20.7 | 0 | 0 | 989 | -12.36 | left cracked open
GV9 |  | 55.2 | 33.8 | 0.4 | 10.6 | 0 | 0 | 989 | -25.78 | Left Open Full
GV9.1 |  | 1.4 | 1.2 | 13.9 | 83.5 | 0 | 0 | 989 | -2.98 | Reg closed bad gas
GV10 |  | 40.2 | 31.8 | 4.5 | 23.5 | 0 | 0 | 989 | 1.69 | Left closed
GV11 |  | 39.9 | 32.5 | 5.5 | 22.1 | 0 | 0 | 989 | 1.21 | Left Off
GV12+R3 |  | 55 | 40.8 | 0.1 | 4.1 | 0 | 0 | 989 | -23.39 | Left Open Full
GV13 |  | 0.7 | 1.8 | 18.7 | 78.8 | 0 | 0 | 989 | 1.58 | Left Off
GV14 |  | 51 | 36.2 | 0 | 12.8 | 0 | 10 | 989 | -27.78 | Left Open Full
GV15 |  | 56.6 | 40.6 | 0 | 2.8 | 0 | 4 | 989 | -15.69 | Left Open Full
GV16 |  | 0.1 | 0 | 20.1 | 79.8 | 0 | 0 | 989 | -13.22 | Reg turned off high o2 bad gas
GV17+LC4 |  | 18.7 | 8 | 14.2 | 59.1 | 0 | 0 | 989 | 0.58 | left off
GV18+21 |  | 46.4 | 38.6 | 0.1 | 14.9 | 0 | 0 | 989 | -18.54 | Left open full
GV19 |  | 37.4 | 25.5 | 3.8 | 33.3 | 0 | 0 | 989 | 1.23 | Left Off
GV20 |  | 0.8 | 1.6 | 19.7 | 77.9 | 0 | 0 | 989 | 0.36 | Left Off
GV 22 + CVs |  | 55.2 | 40.1 | 1 | 3.7 | 0 | 0 | 989 | -27.58 | Reg closed too half way
GV23 |  | 53.9 | 39.7 | 1.1 | 5.3 | 0 | 0 | 989 | -31.24 | Reg closed too half way
GV24 |  | 55.2 | 30.2 | 0.2 | 14.4 | 0 | 0 | 989 | -14.89 | Left Open Full
GV25 |  | 54.1 | 39.6 | 0.5 | 5.8 | 0 | 0 | 989 | -13.36 | Left Open Full
GV26/A |  | 53.9 | 35.1 | 0.6 | 10.4 | 0 | 0 | 989 | -37.58 | Left Open Full
GV27+28 / B+C |  | 51.2 | 35.6 | 0.3 | 12.9 | 0 | 0 | 989 | -22.21 | left open full
GV30 |  | 48.9 | 29.9 | 0.4 | 20.8 | 0 | 0 | 989 | -13.28 | Left open full
GV31 |  | 50.4 | 34 | 1.1 | 14.5 | 0 | 0 | 989 | -14.28 | Left cracked open
GV32 |  | 51.2 | 40.1 | 1 | 7.7 | 0 | 0 | 989 | -15.27 | Reg closed too half way high o2
GV33 |  | 39.9 | 38.9 | 1.4 | 19.8 | 0 | 0 | 989 | -14.23 | Left off
GV34 |  | 56.9 | 31.4 | 1.3 | 10.4 | 0 | 0 | 989 | -20 | Reg closed too cracked
RP6.1 |  | 0.7 | 4.7 | 19.4 | 75.2 | 0 | 0 | 989 | 0.69 | Left Off
LC1B |  | 1.2 | 0.8 | 17.5 | 80.5 | 0 | 0 | 989 | -4.12 | Left Off
LC1.1 |  | 49.9 | 17.5 | 1 | 31.6 | 0 | 0 | 989 | 1 | Reg cracked open
LC2R? |  | 48.1 | 30.8 | 1.1 | 20 | 0 | 0 | 989 | -14.78 | Left cracked Open
GV 2.1 |  | 55.2 | 38.4 | 0.3 | 6.1 | 0 | 0 | 989 | -16.23 | Left Open Full
GV 2.2+ LC2B |  | 51.2 | 33.2 | 0.6 | 15 | 0 | 0 | 989 | -11.28 | Left Open full
GV / LC3.1 + LC3 |  | 31.2 | 24.1 | 7 | 37.7 | 0 | 0 | 989 | 1.06 | left turned off
LC4B |  | 54.2 | 41.2 | 0.4 | 4.2 | 0 | 0 | 989 | -21.39 | Left open full
LC5 |  | 21.3 | 18.9 | 11.2 | 48.6 | 0 | 0 | 989 | 2.87 | Left off
LC6 |  | 30.8 | 22.3 | 8.2 | 38.7 | 0 | 0 | 989 | 1.06 | Left off
GV29D + LC6B |  | 55.4 | 39.6 | 0.4 | 4.6 | 0 | 0 | 989 | -25.63 | Left Open Full
PW1 |  | 35.6 | 13.8 | 3.9 | 46.7 | 0 | 0 | 989 | 1.23 | Left Off bad gas high o2
PW2 |  | 49.8 | 31.2 | 1.1 | 17.9 | 0 | 0 | 989 | -11.27 | Left cracked open
PW3 |  | 14.4 | 14.9 | 8.2 | 62.5 | 0 | 0 | 989 | 2.87 | Well Left Off
PW4 |  | 33.5 | 19.1 | 4 | 43.4 | 0 | 0 | 989 | 1.98 | left off
PW5 |  | 29.8 | 24.1 | 2.2 | 43.9 | 0 | 0 | 989 | 0.87 | left off
PW6 |  | 54.1 | 30.2 | 0.6 | 15.1 | 0 | 1 | 989 | -20.31 | Left Opened Full
Point: Cap Vent |  | Not connected.
Flare | 15:00 | 50.2 | 30.2 | 1 | 18.6 | 0 | 0 | 989 | -35.69 | Gas improved a lot. Engine 560
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-05-16
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 16 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:40 | 41.2 | 33.8 | 1.8 | 23.2 | 0 | 0 | 995 | -34.21
GV1 |  | 39.8 | 29.6 | 1.3 | 29.3 | 0 | 0 | 995 | -11.24 | Reg closed bad gas
GV2 |  | 50.9 | 34.8 | 0.4 | 13.9 | 0 | 0 | 995 | -6.98 | Left Open full
GV3 |  | 56.9 | 31.2 | 0.5 | 11.4 | 0 | 0 | 995 | -19.87 | Left Open Full
GV4 |  | 50.1 | 39.9 | 1 | 9 | 0 | 0 | 995 | -20.36 | Left Cracked Open
GV5+R1 |  | 49.9 | 30.2 | 1.1 | 18.8 | 0 | 0 | 995 | -30.28 | left cracked open
GV6 |  | 56.8 | 39.4 | 0.4 | 3.4 | 0 | 0 | 995 | -29.63 | Left Open full
GV7 |  | 58.6 | 30.2 | 0.5 | 10.7 | 0 | 0 | 995 | -15.64 | Reg opened full good gas
GV8 |  | 48.7 | 30.1 | 1 | 20.2 | 0 | 0 | 995 | -14.23 | left cracked open
GV9 |  | 52.2 | 30.2 | 0.3 | 17.3 | 0 | 0 | 995 | -22.14 | Left Open Full
GV9.1 |  | 1.9 | 1.9 | 12.1 | 84.1 | 0 | 0 | 995 | -3.98 | Left Off bad gas high o2
GV10 |  | 49.9 | 30.2 | 1 | 18.9 | 0 | 0 | 995 | 1.69 | Reg cracked open good gas
GV11 |  | 35.2 | 30.9 | 5.1 | 28.8 | 0 | 0 | 995 | 1.01 | Left Off
GV12+R3 |  | 57.4 | 39.6 | 0.3 | 2.7 | 0 | 0 | 995 | -22.89 | Left Open Full
GV13 |  | 0.9 | 1.7 | 19.1 | 78.3 | 0 | 0 | 995 | 1.89 | Left Off
GV14 |  | 50.2 | 38.9 | 0.1 | 10.8 | 0 | 13 | 995 | -25.63 | Left Open Full
GV15 |  | 55.9 | 41.2 | 0.3 | 2.6 | 0 | 5 | 995 | -14.12 | Left Open Full
GV16 |  | 0.4 | 0.5 | 19.9 | 79.2 | 0 | 0 | 995 | -10.23 | Left Off
GV17+LC4 |  | 19.9 | 7.4 | 13.2 | 59.5 | 0 | 0 | 995 | 0.89 | left off
GV18+21 |  | 53.8 | 35.2 | 0.3 | 10.7 | 0 | 0 | 995 | -17.48 | Left open full
GV19 |  | 35.6 | 24.1 | 2.2 | 38.1 | 0 | 0 | 995 | 1.58 | Left Off
GV20 |  | 1.1 | 1.2 | 18.4 | 79.3 | 0 | 0 | 995 | 0.56 | Left Off
GV 22 + CVs |  | 42.3 | 39.5 | 1.9 | 16.3 | 0 | 0 | 995 | -29.69 | Reg closed bad gas
GV23 |  | 44.5 | 36.4 | 1.4 | 17.7 | 0 | 0 | 995 | -30.21 | Reg closed bad gas
GV24 |  | 54.2 | 31.1 | 0.3 | 14.4 | 0 | 0 | 995 | -15.63 | Left Open Full
GV25 |  | 52.3 | 38.4 | 0.6 | 8.7 | 0 | 0 | 995 | -14.12 | Left Open Full
GV26/A |  | 56.9 | 36.9 | 0.4 | 5.8 | 0 | 0 | 995 | -35.21 | Left Open Full
GV27+28 / B+C |  | 52.1 | 34.1 | 0.2 | 13.6 | 0 | 0 | 995 | -25.96 | left open full
GV30 |  | 50.3 | 30.2 | 0.6 | 18.9 | 0 | 0 | 995 | -14.78 | Left open full
GV31 |  | 49.9 | 33.2 | 1 | 15.9 | 0 | 0 | 995 | -15.69 | Left cracked open
GV32 |  | 52.3 | 39.4 | 1.2 | 7.1 | 0 | 0 | 995 | -14.28 | Left open half way
GV33 |  | 37.1 | 36.5 | 1.9 | 24.5 | 0 | 0 | 995 | -13.21 | Left off
GV34 |  | 50.1 | 30.9 | 1.1 | 17.9 | 0 | 0 | 995 | -19.87 | Left cracked open
RP6.1 |  | 0.9 | 5 | 19.9 | 74.2 | 0 | 0 | 995 | 0.89 | Left Off
LC1B |  | 1.5 | 0.9 | 17.9 | 79.7 | 0 | 0 | 995 | -5.23 | Left Off
LC1.1 |  | 52.1 | 18 | 1.1 | 28.8 | 0 | 0 | 995 | 1.23 | Left Cracked Open
LC2R? |  | 50.3 | 31.7 | 1.1 | 16.9 | 0 | 0 | 995 | -15.21 | Left cracked Open
GV 2.1 |  | 56.6 | 35.8 | 0.4 | 7.2 | 0 | 0 | 995 | -14.77 | Left Open Full
GV 2.2+ LC2B |  | 52.2 | 35.7 | 1 | 11.1 | 0 | 0 | 995 | -12.33 | Reg closed too cracked high o2
GV / LC3.1 + LC3 |  | 33.9 | 25.4 | 6.9 | 33.8 | 0 | 0 | 995 | 1.87 | left turned off
LC4B |  | 53.6 | 39.4 | 0.5 | 6.5 | 0 | 0 | 995 | -22.39 | Left open full
LC5 |  | 22.5 | 20 | 9.9 | 47.6 | 0 | 0 | 995 | 2.77 | Left off
LC6 |  | 31.8 | 25.6 | 7.8 | 34.8 | 0 | 0 | 995 | 1.28 | Left off
GV29D + LC6B |  | 59.9 | 31.2 | 0.1 | 8.8 | 0 | 0 | 995 | -24.43 | Left Open Full
PW1 |  | 35.6 | 12 | 4.2 | 48.2 | 0 | 0 | 995 | 1.89 | Left Off bad gas high o2
PW2 |  | 53.1 | 12.1 | 1.1 | 33.7 | 0 | 0 | 995 | -12.34 | Left cracked open
PW3 |  | 13.6 | 15 | 7.9 | 63.5 | 0 | 0 | 995 | 2.99 | Well Left Off
PW4 |  | 34.8 | 19.7 | 5 | 40.5 | 0 | 0 | 995 | 1.02 | left off
PW5 |  | 30.2 | 25.6 | 2.5 | 41.7 | 0 | 0 | 995 | 1.23 | left off
PW6 |  | 53.7 | 29.6 | 0.9 | 15.8 | 0 | 4 | 995 | -15.89 | Left Opened Full
Point: Cap Vent |  | Not connected.
Flare | 15:45 | 48.9 | 27.8 | 0.9 | 22.4 | 0 | 0 | 995 | -32.47 | Gas improved a lot. Engine 560
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-05-21
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 19 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 11:35 | 38.2 | 22.7 | 2.5 | 36.6 | 0 | 0 | 993 | -31.6
GV1 |  | 0.3 | 0.3 | 20.6 | 78.8 | 0 | 0 | 993 | -9.5 | left Off
GV2 |  | 51.9 | 36.9 | 0.2 | 11 | 0 | 0 | 993 | -32.4 | Left Open full
GV3 |  | 64 | 37.4 | 0.1 | -1.5 | 0 | 0 | 993 | -30.7 | Left Open full
GV4 |  | 29 | 31.3 | 0.1 | 39.6 | 0 | 0 | 993 | -27.9 | Reg closed bad gas
GV5+R1 |  | 39.6 | 26.5 | 6.8 | 27.1 | 0 | 0 | 993 | -30.8 | Reg closed high o2
GV6 |  | 57.9 | 39 | 0.2 | 2.9 | 0 | 0 | 993 | -30.7 | Left Open Full
GV7 |  | 49 | 32.1 | 3 | 15.9 | 0 | 0 | 994 | -30.3 | reg closed too cracked open
GV8 |  | 34.7 | 25.2 | 4.1 | 36 | 2 | 0 | 992 | 3.4 | Left Off
GV9 |  | 58.6 | 38.2 | 0.3 | 2.9 | 0 | 0 | 992 | -35.8 | Left Open Full
GV9.1 |  | 0.2 | 0.2 | 19.7 | 79.9 | 0 | 0 | 992 | 0.81 | left off
GV10 |  | 58.6 | 34.4 | 0.4 | 6.6 | 0 | 0 | 992 | -35.7 | Left cracked open
GV11 |  | 59.2 | 40.1 | 0.2 | 0.5 | 0 | 0 | 992 | -30.6 | Reg cracked open
GV12+R3 |  | 58.2 | 40.4 | 0.1 | 1.3 | 0 | 0 | 992 | -31.9 | Left Open Full
GV13 |  | 0.4 | 2 | 17.8 | 79.8 | 0 | 0 | 992 | 0.4 | Left Off
GV14 |  | 50.2 | 35.2 | 0.3 | 14.3 | 0 | 7 | 990 | -35.3 | Left Open Full
GV15 |  | 54.2 | 40.4 | 0.3 | 5.1 | 0 | 2 | 990 | -34.7 | Left Open Full
GV16 |  | 0.1 | 0 | 19.8 | 80.1 | 0 | 0 | 992 | -14.2 | left off
GV17+LC4 |  | 23.7 | 12.4 | 11.8 | 52.1 | 0 | 0 | 990 | 0.5 | Left off
GV18+21 |  | 47.7 | 39.2 | 0.4 | 12.7 | 0 | 0 | 990 | -35.2 | Left open full
GV19 |  | 33.6 | 21.1 | 7 | 38.3 | 0 | 0 | 990 | 1 | Left Off
GV20 |  | 0.2 | 0.5 | 19.3 | 80 | 0 | 0 | 990 | 0.35 | Left Off
GV 22 + CVs |  | 0.2 | 3 | 18.4 | 78.4 | 0 | 0 | 993 | 0.4 | Left Off
GV23 |  | 0.2 | 6 | 15.5 | 78.3 | 0 | 0 | 993 | 0.04 | Left Off
GV24 |  | 59.5 | 42.5 | 0.3 | -2.3 | 0 | 0 | 993 | -32 | Left Open Full
GV25 |  | 46.3 | 39.6 | 0.3 | 13.8 | 0 | 0 | 993 | -32.1 | Left Open Full
GV26/A |  | 49.1 | 36.9 | 1.6 | 12.4 | 0 | 0 | 993 | -32 | Reg closed to cracked
GV27+28 / B+C |  | 47 | 37 | 0.2 | 15.8 | 0 | 0 | 993 | -31.6 | left open full
GV30 |  | 45.3 | 36.5 | 0.3 | 17.9 | 0 | 0 | 989 | -26.2 | Left Open Full
GV31 |  | 54.3 | 40.1 | 0.3 | 5.3 | 0 | 0 | 989 | -26.4 | Reg opened full
GV32 |  | 35.4 | 30.8 | 1.4 | 32.4 | 0 | 0 | 989 | -26.8 | reg closed bad gas
GV33 |  | 47.5 | 36.3 | 0.5 | 15.7 | 0 | 0 | 989 | -15.1 | Reg cracked open
GV34 |  | 26.1 | 19.2 | 7 | 47.7 | 0 | 0 | 989 | -24.7 | Reg closed
RP6.1 |  | 0.3 | 0.6 | 20.8 | 78.3 | 0 | 0 | 993 | -14.4 | Left Off
LC1B |  | 0.2 | 0.2 | 19.5 | 80.1 | 0 | 0 | 992 | -4.6 | left Off
LC1.1 |  | 56.9 | 4.1 | 0.4 | 38.6 | 0 | 0 | 993 | -32 | Reg opened full
LC2R? |  | 54.4 | 34.1 | 0.3 | 11.2 | 0 | 0 | 994 | -29.8 | Reg Opened Full
GV 2.1 |  | 54.3 | 40 | 1.2 | 4.5 | 0 | 0 | 993 | -32 | Left Open full
GV 2.2+ LC2B |  | 31.5 | 23.8 | 8.1 | 36.6 | 0 | 0 | 993 | -28.2 | Closed bad gas
GV / LC3.1 + LC3 |  | 0.1 | 0.1 | 19.6 | 80.2 | 0 | 0 | 992 | -12.1 | Left off
LC4B |  | 38 | 31.8 | 1.9 | 28.3 | 0 | 0 | 990 | -36.4 | reg closed too cracked open
LC5 |  | 31.9 | 18.9 | 6.9 | 42.3 | 0 | 0 | 990 | -9.26 | Left off
LC6 |  | 28.4 | 25.2 | 4.2 | 42.2 | 0 | 0 | 990 | -8.14 | Left off
GV29D + LC6B |  | 56.8 | 41.3 | 0.3 | 1.6 | 0 | 0 | 993 | -31.7 | Left Open Full
PW1 |  | 34.2 | 18.1 | 2.6 | 45.1 | 0 | 0 | 993 | 1.98 | Left Off bad gas high o2
PW2 |  | 49.6 | 16.2 | 0.9 | 33.3 | 0 | 0 | 993 | -8.1 | left Cracked Open
PW3 |  | 16.2 | 18.9 | 4.1 | 60.8 | 0 | 0 | 993 | -0.1 | Well Left Off
PW4 |  | 28.4 | 11.7 | 3.2 | 56.7 | 0 | 0 | 993 | 1.1 | left off
PW5 |  | 31.8 | 13.8 | 2.6 | 51.8 | 0 | 0 | 993 | -0.4 | left off
PW6 |  | 49.9 | 30.1 | 0.3 | 19.7 | 0 | 0 | 993 | -6.2 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 15:20 | 40.3 | 23.2 | 1.9 | 34.6 | 3 | 0 | 992 | -37.9 | Gas improved a lot. Engine 560
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-05-30
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 17 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 12:10 | 39.9 | 23.9 | 1.6 | 34.6 | 0 | 0 | 999 | -30.23
GV1 |  | 0.5 | 0.4 | 19.9 | 79.2 | 0 | 0 | 999 | -10.12 | left Off
GV2 |  | 52.3 | 33.1 | 0.3 | 14.3 | 0 | 0 | 999 | -31.29 | Left Open full
GV3 |  | 61.2 | 35.6 | 0.3 | 2.9 | 0 | 0 | 999 | -31.27 | Left Open full
GV4 |  | 43.9 | 30.8 | 0.4 | 24.9 | 1 | 0 | 999 | -28.11 | Reg cracked open good gas
GV5+R1 |  | 44.9 | 25.6 | 1.1 | 28.4 | 0 | 0 | 999 | -30.56 | Reg cracked open good gas
GV6 |  | 55.2 | 36.9 | 0.3 | 7.6 | 0 | 0 | 999 | -30.98 | Left Open Full
GV7 |  | 45.6 | 30.6 | 1.1 | 22.7 | 0 | 0 | 999 | -29.98 | Reg opened too half way
GV8 |  | 36.9 | 24.7 | 3.9 | 34.5 | 4 | 0 | 999 | 3.56 | Left Off
GV9 |  | 55.9 | 36.4 | 0.4 | 7.3 | 0 | 0 | 999 | -33.21 | Left Open Full
GV9.1 |  | 1.3 | 0.3 | 19.4 | 79 | 0 | 0 | 999 | 0.78 | left off
GV10 |  | 56.9 | 31.4 | 0.5 | 11.2 | 0 | 0 | 999 | -34.59 | Left cracked open ( gas drops quickly if open full)
GV11 |  | 59.2 | 40.1 | 0.2 | 0.5 | 0 | 0 | 999 | -30.69 | Reg opened too half way good gas
GV12+R3 |  | 55.2 | 38.7 | 0.3 | 5.8 | 0 | 0 | 999 | -32.58 | Left Open Full
GV13 |  | 0.4 | 2.6 | 16.9 | 80.1 | 0 | 0 | 999 | 0.48 | Left Off
GV14 |  | 50.2 | 33.4 | 0.5 | 15.9 | 0 | 8 | 999 | -34.59 | Left Open Full
GV15 |  | 51.3 | 38.6 | 0.3 | 9.8 | 0 | 5 | 999 | -32.87 | Left Open Full
GV16 |  | 0.5 | 0.5 | 19.1 | 79.9 | 0 | 0 | 999 | -15.23 | left off
GV17+LC4 |  | 22.1 | 11.8 | 11 | 55.1 | 0 | 0 | 999 | 0.45 | Left off
GV18+21 |  | 48.1 | 38.6 | 0.5 | 12.8 | 0 | 0 | 999 | -34.78 | Left open full
GV19 |  | 32.1 | 20.1 | 6 | 41.8 | 0 | 0 | 999 | 1.23 | Left Off
GV20 |  | 0.3 | 0.6 | 19.1 | 80 | 0 | 0 | 999 | 0.45 | Left Off
GV 22 + CVs |  | 0.5 | 3.2 | 18.6 | 77.7 | 0 | 0 | 999 | 0.36 | Left Off
GV23 |  | 0.3 | 7 | 15.1 | 77.6 | 1 | 0 | 999 | 0.1 | Left Off
GV24 |  | 58.6 | 40.1 | 0.4 | 0.9 | 0 | 0 | 999 | -32.56 | Left Open Full
GV25 |  | 45.8 | 38.5 | 0.2 | 15.5 | 0 | 0 | 999 | -34.78 | Left Open Full
GV26/A |  | 49.6 | 33.2 | 1.3 | 15.9 | 0 | 0 | 999 | -33.69 | Reg opened too half way
GV27+28 / B+C |  | 46.9 | 35.8 | 0.3 | 17 | 0 | 2 | 999 | -32.14 | left open full
GV30 |  | 48.9 | 33.6 | 0.4 | 17.1 | 0 | 0 | 999 | -27.89 | Left Open Full
GV31 |  | 49.1 | 39.6 | 1.3 | 10 | 0 | 0 | 999 | -26.99 | Reg closed to half way o2 creeped up
GV32 |  | 44.5 | 31.5 | 1.2 | 22.8 | 1 | 0 | 999 | -27.01 | Reg cracked open
GV33 |  | 39.6 | 32.8 | 1.3 | 26.3 | 0 | 0 | 999 | -16.23 | Reg closed bad gas
GV34 |  | 46.6 | 27.4 | 0.9 | 25.1 | 0 | 0 | 999 | -23.69 | Reg cracked open good gas
RP6.1 |  | 0.4 | 0.5 | 19.6 | 79.5 | 0 | 0 | 999 | -14.89 | Left Off
LC1B |  | 0.6 | 0.4 | 19.1 | 79.9 | 0 | 0 | 999 | -5.23 | left Off
LC1.1 |  | 55.9 | 3.4 | 0.3 | 40.4 | 0 | 0 | 999 | -30.14 | Left Open Full
LC2R? |  | 51.4 | 31.8 | 0.1 | 16.7 | 0 | 0 | 999 | -29.36 | Left Open Full
GV 2.1 |  | 52.3 | 39.4 | 0.2 | 8.1 | 0 | 0 | 999 | -31.24 | Left Open full
GV 2.2+ LC2B |  | 31.5 | 23.8 | 8.1 | 36.6 | 0 | 0 | 999 | -29.36 | Left Off
GV / LC3.1 + LC3 |  | 0.4 | 0.2 | 7.5 | 91.9 | 0 | 0 | 999 | -14.28 | Left off
LC4B |  | 45.6 | 32.5 | 1.1 | 20.8 | 0 | 0 | 999 | -30.25 | Reg opened half way
LC5 |  | 32.4 | 19.2 | 7 | 41.4 | 0 | 0 | 999 | -10.23 | Left off
LC6 |  | 25.3 | 25.9 | 4.9 | 43.9 | 0 | 0 | 999 | -9.98 | Left off
GV29D + LC6B |  | 55.9 | 39.4 | 0.5 | 4.2 | 0 | 0 | 999 | -30.28 | Left Open Full
PW1 |  | 35.6 | 17.9 | 2.5 | 44 | 0 | 0 | 999 | 1.56 | Left Off bad gas high o2
PW2 |  | 46.9 | 17.9 | 1.2 | 34 | 0 | 0 | 999 | -6.99 | left Cracked Open
PW3 |  | 17.2 | 19.2 | 4.9 | 58.7 | 0 | 0 | 999 | -0.28 | Well Left Off
PW4 |  | 29.9 | 13.9 | 3.5 | 52.7 | 0 | 0 | 999 | 1.48 | left off
PW5 |  | 33.6 | 14.2 | 3 | 49.2 | 0 | 0 | 999 | -0.58 | left off
PW6 |  | 50.1 | 29.6 | 0.04 | 20.26 | 0 | 0 | 999 | -7.45 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 16:25 | 44.4 | 24.9 | 1.2 | 29.5 | 5 | 0 | 999 | -36.98 | Gas improved a lot. Engine 560

## June
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-06-05
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:48 | 0.4 | 0.9 | 20.3 | 78.4 | 0 | 0 | 998 | -0.25 | 1 | 8.8
BK BH 3 | 10:53 | 0.3 | 1.2 | 20.5 | 78 | 0 | 0 | 998 | 0.41 | 1 | 3.1
BK BH 4 | 10:54 | 0 | 1.8 | 19.6 | 78.6 | 0 | 0 | 998 | 0.23 | 1 | 5.1
BK BH 5 | 10:56 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 998 | 0.58 | 1 | 1.5
BK BH 6 | 11:00 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | 0.26 | 1 | 1.5
BK BH 7 | 11:04 | 0 | 2.5 | 20.1 | 77.4 | 0 | 0 | 998 | 0.45 | 1 | 10
BK BH 8 | 11:07 | 30.1 | 1.2 | 20.2 | 48.5 | 0 | 0 | 998 | -0.12 | 32.2 | 3.6
BK BH 9 | 11:13 | 26.2 | 5.6 | 19.9 | 48.3 | 0 | 0 | 998 | 0.36 | 29.6 | 10.4
BK BH 10 | 11:18 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 998 | -0.15 | 1 | 3.9
BK BH 11 | 11:30 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 998 | 0.73 | 1 | 6.5
BK BH 12 | 11:34 | 0 | 1.9 | 19.2 | 78.9 | 0 | 0 | 998 | -0.42 | 1 | 6.6
BK BH 13 | 11:38 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 998 | 0.36 | 1 | 9.4
BK BH 14 | 11:41 | 0 | 1.3 | 20.4 | 78.3 | 0 | 0 | 998 | -0.11 | 1 | 3.5
BK BH 15 | 11:44 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 998 | 0.74 | 1 | 17.6
BK BH 16 | 11:47 | 0.4 | 1.4 | 20.7 | 77.5 | 0 | 0 | 998 | 0.23 | 1 | 11.4
BK BH 17 | 11:54 | 0.3 | 0.3 | 19.6 | 79.8 | 0 | 0 | 998 | -0.18 | 1 | 12.9
BK BH 18 | 10:20 | 2 | 2.5 | 20.2 | 75.3 | 0 | 0 | 998 | 0.92 | 6.8 | 21.2
BK BH 19 | 10:24 | 0.8 | 1.4 | 19.9 | 77.9 | 0 | 0 | 998 | 0.37 | 1 | 11.2
BK BH 20 | 10:27 | 0.6 | 5.2 | 19.5 | 74.7 | 0 | 0 | 998 | -0.18 | 1 | 10.7
BK BH 21 | 10:32 | 0.4 | 9 | 20.1 | 70.5 | 0 | 0 | 998 | 0.29 | 1 | 21.7
BK BH 23 | 10:37 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 998 | -0.11 | 1 | 7.3
BK BH 24 | 10:40 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 998 | 0.54 | 1 | 1.5
BK BH 25 | 10:44 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 998 | 0.87 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-06-12
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 22 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:10 | 0.2 | 1.1 | 19.9 | 78.8 | 0 | 0 | 1002 | -0.52 | 1 | 8.8
BK BH 3 | 10:15 | 0.2 | 1.3 | 20.1 | 78.4 | 0 | 0 | 1002 | 0.23 | 1 | 3.1
BK BH 4 | 10:17 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.45 | 1 | 5.1
BK BH 5 | 10:19 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 1002 | 0.21 | 1 | 1.5
BK BH 6 | 10:22 | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1002 | 0.18 | 1 | 1.5
BK BH 7 | 10:26 | 0 | 2.9 | 20.3 | 76.8 | 0 | 0 | 1002 | -0.45 | 1 | 10
BK BH 8 | 10:29 | 30.9 | 1.4 | 20.4 | 47.3 | 0 | 0 | 1002 | 0.68 | 32.2 | 3.6
BK BH 9 | 10:35 | 27.4 | 5 | 19.5 | 48.1 | 0 | 0 | 1002 | -0.19 | 29.6 | 10.4
BK BH 10 | 10:40 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 1002 | 0.38 | 1 | 3.9
BK BH 11 | 10:52 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1002 | -0.45 | 1 | 6.5
BK BH 12 | 10:56 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.62 | 1 | 6.6
BK BH 13 | 11:00 | 0 | 1.1 | 20.3 | 78.6 | 0 | 0 | 1002 | 0.54 | 1 | 9.4
BK BH 14 | 11:03 | 0 | 1.6 | 20.1 | 78.3 | 0 | 0 | 1002 | -0.75 | 1 | 3.5
BK BH 15 | 11:06 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 1002 | 0.62 | 1 | 17.6
BK BH 16 | 11:09 | 0.5 | 1.2 | 20.4 | 77.9 | 0 | 0 | 1002 | -0.38 | 1 | 11.4
BK BH 17 | 11:16 | 0.2 | 0.5 | 19.9 | 79.4 | 0 | 0 | 1002 | -0.42 | 1 | 12.9
BK BH 18 | 9:42 | 2.2 | 2.1 | 20.3 | 75.4 | 0 | 0 | 1002 | 0.28 | 6.8 | 21.2
BK BH 19 | 9:46 | 0.8 | 1.2 | 19.8 | 78.2 | 0 | 0 | 1002 | -0.58 | 1 | 11.2
BK BH 20 | 9:49 | 0.6 | 5.4 | 20.4 | 73.6 | 0 | 0 | 1002 | -0.36 | 1 | 10.7
BK BH 21 | 9:54 | 0.5 | 8.8 | 20.3 | 70.4 | 0 | 0 | 1002 | -0.89 | 1 | 21.7
BK BH 23 | 9:59 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1002 | 0.27 | 1 | 7.3
BK BH 24 | 10:02 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | -0.24 | 1 | 1.5
BK BH 25 | 10:06 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1002 | -0.28 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-06-19
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0.1 | 1.4 | 20.1 | 78.4 | 0 | 0 | 997 | -0.53 | 1 | 8.8
BK BH 3 | 10:41 | 0.3 | 1.6 | 20.3 | 77.8 | 0 | 0 | 997 | 0.42 | 1 | 3.1
BK BH 4 | 10:43 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 997 | 0.52 | 1 | 5.1
BK BH 5 | 10:46 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 997 | 0.47 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 997 | -0.17 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 997 | 0.64 | 1 | 10
BK BH 8 | 10:55 | 31.2 | 1.2 | 19.9 | 47.7 | 0 | 0 | 997 | 0.29 | 32.2 | 3.6
BK BH 9 | 11:01 | 28.2 | 4.8 | 19.2 | 47.8 | 0 | 0 | 997 | -0.15 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 2 | 19.3 | 78.7 | 0 | 0 | 997 | 0.36 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 2.3 | 20.3 | 77.4 | 0 | 0 | 997 | -0.52 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 1.1 | 20.2 | 78.7 | 0 | 0 | 997 | 0.14 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | -0.78 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 997 | 0.96 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 997 | 0.32 | 1 | 17.6
BK BH 16 | 11:35 | 0.4 | 1.4 | 20.3 | 77.9 | 0 | 0 | 997 | -0.14 | 1 | 11.4
BK BH 17 | 11:42 | 0.2 | 0.8 | 20.1 | 78.9 | 0 | 0 | 997 | 0.25 | 1 | 12.9
BK BH 18 | 10:08 | 1.9 | 3 | 20.1 | 75 | 0 | 0 | 997 | -0.78 | 6.8 | 21.2
BK BH 19 | 10:12 | 0.7 | 1.6 | 19.4 | 78.3 | 0 | 0 | 997 | 0.63 | 1 | 11.2
BK BH 20 | 10:15 | 0.3 | 5.1 | 19.8 | 74.8 | 0 | 0 | 997 | 0.87 | 1 | 10.7
BK BH 21 | 10:20 | 0.4 | 8.9 | 19.2 | 71.5 | 0 | 0 | 997 | 0.25 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 1.4 | 18.9 | 79.7 | 0 | 0 | 997 | -0.11 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 997 | 0.54 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 997 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-06-26
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 23 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:58 | 0.2 | 1.9 | 20.1 | 77.8 | 0 | 0 | 999 | 0.49 | 1 | 8.8
BK BH 3 | 11:03 | 0.4 | 1.4 | 20.3 | 77.9 | 0 | 0 | 999 | -0.62 | 1 | 3.1
BK BH 4 | 11:04 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 999 | 0.32 | 1 | 5.1
BK BH 5 | 11:06 | 0 | 0.7 | 19.5 | 79.8 | 0 | 0 | 999 | 0.87 | 1 | 1.5
BK BH 6 | 11:10 | 0 | 0.7 | 19.3 | 80 | 0 | 0 | 999 | 0.75 | 1 | 1.5
BK BH 7 | 11:14 | 0 | 2.8 | 20.1 | 77.1 | 0 | 0 | 999 | 0.36 | 1 | 10
BK BH 8 | 11:17 | 30.9 | 1.3 | 19.9 | 47.9 | 0 | 0 | 999 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:23 | 29 | 4.4 | 19.2 | 47.4 | 0 | 0 | 999 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:28 | 0 | 1.8 | 19.3 | 78.9 | 0 | 0 | 999 | 0.69 | 1 | 3.9
BK BH 11 | 11:40 | 0 | 2.5 | 20.3 | 77.2 | 0 | 0 | 999 | -0.15 | 1 | 6.5
BK BH 12 | 11:44 | 0 | 1.6 | 20.2 | 78.2 | 0 | 0 | 999 | 0.24 | 1 | 6.6
BK BH 13 | 11:48 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 999 | -0.63 | 1 | 9.4
BK BH 14 | 11:51 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 999 | 0.21 | 1 | 3.5
BK BH 15 | 11:54 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 999 | 0.02 | 1 | 17.6
BK BH 16 | 11:57 | 0.5 | 1.6 | 20.3 | 77.6 | 0 | 0 | 999 | 0.58 | 1 | 11.4
BK BH 17 | 12:04 | 0.4 | 1.1 | 20.1 | 78.4 | 0 | 0 | 999 | 0.77 | 1 | 12.9
BK BH 18 | 10:30 | 1.5 | 2.9 | 20.1 | 75.5 | 0 | 0 | 999 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:34 | 0.4 | 1.4 | 19.4 | 78.8 | 0 | 0 | 999 | 0.38 | 1 | 11.2
BK BH 20 | 10:37 | 0.6 | 5.5 | 19.8 | 74.1 | 0 | 0 | 999 | -0.25 | 1 | 10.7
BK BH 21 | 10:42 | 0.2 | 9.9 | 19.2 | 70.7 | 0 | 0 | 999 | 0.14 | 1 | 21.7
BK BH 23 | 10:47 | 0 | 1.2 | 18.9 | 79.9 | 0 | 0 | 999 | 0.75 | 1 | 7.3
BK BH 24 | 10:50 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 999 | -0.63 | 1 | 1.5
BK BH 25 | 10:54 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 999 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-06-06
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 18 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 12:00 | 39.1 | 33.6 | 1.4 | 25.9 | 0 | 0 | 998 | -30.62
GV1 |  | 0.4 | 0.4 | 19.9 | 79.3 | 0 | 0 | 998 | -10.23 | left Off
GV2 |  | 50 | 34.1 | 0.3 | 15.6 | 0 | 0 | 998 | -30.25 | Left Open full
GV3 |  | 61.2 | 35.2 | 0.3 | 3.3 | 0 | 0 | 998 | -31.89 | Left Open full
GV4 |  | 35.2 | 30.8 | 0.9 | 33.1 | 0 | 0 | 998 | -28.96 | Reg closed bad gas
GV5+R1 |  | 38.7 | 25.2 | 3.9 | 32.2 | 0 | 0 | 998 | -32.14 | Reg closed high o2
GV6 |  | 55.2 | 36.1 | 0.3 | 8.4 | 0 | 0 | 998 | -29.39 | Left Open Full
GV7 |  | 48.2 | 33.5 | 1.6 | 16.7 | 0 | 0 | 998 | -29.74 | reg closed too cracked open
GV8 |  | 33.9 | 23.7 | 4 | 38.4 | 2 | 0 | 998 | 3.58 | Left Off
GV9 |  | 55.8 | 35.2 | 0.2 | 8.8 | 0 | 0 | 998 | -36.98 | Left Open Full
GV9.1 |  | 0.4 | 0.5 | 19.6 | 79.5 | 0 | 0 | 998 | 0.78 | left off
GV10 |  | 55.1 | 33.2 | 0.5 | 11.2 | 0 | 0 | 998 | -34.21 | Left cracked open
GV11 |  | 52.3 | 39.6 | 0.3 | 7.8 | 0 | 0 | 998 | -31.56 | Reg Opened full
GV12+R3 |  | 55.2 | 39.4 | 0.2 | 5.2 | 0 | 0 | 998 | -32 | Left Open Full
GV13 |  | 0.6 | 2.8 | 16.3 | 80.3 | 0 | 0 | 998 | 0.59 | Left Off
GV14 |  | 51.2 | 36.5 | 0.4 | 11.9 | 0 | 5 | 998 | -33.69 | Left Open Full
GV15 |  | 53.9 | 39.4 | 0.2 | 6.5 | 0 | 3 | 998 | -34.78 | Left Open Full
GV16 |  | 0.6 | 0.1 | 19.5 | 79.8 | 0 | 0 | 998 | -16.93 | left off
GV17+LC4 |  | 22.1 | 11.3 | 12 | 54.6 | 0 | 0 | 998 | 0.45 | Left off
GV18+21 |  | 48.9 | 36.2 | 0.3 | 14.6 | 0 | 0 | 998 | -31.27 | Left open full
GV19 |  | 32.8 | 20.7 | 6.9 | 39.6 | 0 | 0 | 998 | 1.06 | Left Off
GV20 |  | 0.1 | 0.4 | 18.5 | 81 | 0 | 0 | 998 | 0.39 | Left Off
GV 22 + CVs |  | 0.4 | 3.6 | 18.1 | 77.9 | 0 | 0 | 998 | 0.55 | Left Off
GV23 |  | 0.3 | 5.2 | 16 | 78.5 | 0 | 0 | 998 | 0.1 | Left Off
GV24 |  | 45.8 | 40.1 | 0.2 | 13.9 | 0 | 0 | 998 | -30.98 | Left Open Full
GV25 |  | 48.9 | 35.2 | 0.6 | 15.3 | 0 | 0 | 998 | -34.52 | Left Open Full
GV26/A |  | 46.9 | 33.8 | 1.5 | 17.8 | 0 | 0 | 998 | -32.58 | Reg closed to cracked
GV27+28 / B+C |  | 47.8 | 38.9 | 0.3 | 13 | 0 | 0 | 998 | -30.99 | left open full
GV30 |  | 46 | 37.4 | 0.4 | 16.2 | 0 | 0 | 998 | -25.69 | Left Open Full
GV31 |  | 53.2 | 39.6 | 0.5 | 6.7 | 0 | 0 | 998 | -27.87 | Reg opened full
GV32 |  | 34.5 | 31.2 | 1.2 | 33.1 | 0 | 0 | 998 | -28.93 | reg closed bad gas
GV33 |  | 45.6 | 35.2 | 0.6 | 18.6 | 0 | 0 | 998 | -14.52 | Reg cracked open
GV34 |  | 25 | 18.4 | 6 | 50.6 | 0 | 0 | 998 | -25 | Reg closed
RP6.1 |  | 0.4 | 1.1 | 20 | 78.5 | 0 | 0 | 998 | -14.99 | Left Off
LC1B |  | 1 | 0.5 | 19.8 | 78.7 | 0 | 0 | 998 | -5.23 | left Off
LC1.1 |  | 55.3 | 3 | 0.5 | 41.2 | 0 | 0 | 998 | -33.96 | Left Open Full
LC2R? |  | 52.1 | 33.1 | 0.4 | 14.4 | 0 | 0 | 998 | -30.38 | Left Open Full
GV 2.1 |  | 55.8 | 39.6 | 1 | 3.6 | 0 | 0 | 998 | -31.47 | Left Open full
GV 2.2+ LC2B |  | 38.6 | 22.1 | 3 | 36.3 | 0 | 0 | 998 | -21.39 | Left Off
GV / LC3.1 + LC3 |  | 0.1 | 0.1 | 20 | 79.8 | 0 | 0 | 998 | -14.58 | Left off
LC4B |  | 40.1 | 32 | 1.5 | 26.4 | 0 | 0 | 998 | -35.96 | reg closed too cracked open
LC5 |  | 30 | 19 | 6 | 45 | 0 | 0 | 998 | -10 | Left off
LC6 |  | 31.2 | 26.3 | 4.6 | 37.9 | 0 | 0 | 998 | -8.45 | Left off
GV29D + LC6B |  | 55.9 | 40.2 | 0.4 | 3.5 | 0 | 0 | 998 | -30.21 | Left Open Full
PW1 |  | 35.8 | 18.9 | 2.1 | 43.2 | 0 | 0 | 998 | 1.57 | Left Off bad gas high o2
PW2 |  | 40 | 15.8 | 0.5 | 43.7 | 0 | 0 | 998 | -9.63 | left Cracked Open
PW3 |  | 17.1 | 16.2 | 4.3 | 62.4 | 0 | 0 | 998 | 0.15 | Well Left Off
PW4 |  | 27.1 | 11.9 | 3 | 58 | 0 | 0 | 998 | 1.23 | left off
PW5 |  | 32.9 | 14 | 2.2 | 50.9 | 0 | 0 | 998 | -0.57 | left off
PW6 |  | 48.1 | 29.6 | 0.4 | 21.9 | 0 | 0 | 998 | -7.14 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 16:00 | 41.2 | 22.3 | 1.1 | 35.4 | 4 | 0 | 998 | -38.31 | Gas improved a lot. Engine 560
Please Note:
Chevrons (>>>) Indicate reading is out of range.
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-06-12
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 22 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:00 | 34.5 | 31.3 | 2.1 | 32.1 | 0 | 0 | 1009 | -30.24
GV1 |  | 0.5 | 0.6 | 19.7 | 79.2 | 0 | 0 | 1009 | -12.36 | left Off
GV2 |  | 49.9 | 33.2 | 0.4 | 16.5 | 0 | 0 | 1009 | -35.24 | Left Open full
GV3 |  | 66.8 | 32 | 0.4 | 0.8 | 0 | 0 | 1009 | -76.9 | Left Open full
GV4 |  | 30.6 | 30.7 | 0.4 | 38.3 | 0 | 0 | 1009 | -1.2 | Left Off bad gas
GV5+R1 |  | 39.3 | 25.4 | 6.5 | 28.8 | 0 | 0 | 1009 | -19.7 | Left Off bad gas
GV6 |  | 53.6 | 31.9 | 0.4 | 14.1 | 0 | 0 | 1009 | -29.63 | Left Open Full
GV7 |  | 45.6 | 30.8 | 1.2 | 22.4 | 0 | 0 | 1009 | -27.58 | Left cracked open
GV8 |  | 31 | 22.1 | 3.6 | 43.3 | 2 | 0 | 1009 | 4 | Left Off
GV9 |  | 49.2 | 37.5 | 0.5 | 12.8 | 0 | 0 | 1009 | -79.4 | Left Open Full
GV9.1 |  | 0.4 | 0.1 | 19.8 | 79.7 | 0 | 0 | 1009 | 1.02 | left off
GV10 |  | 23.2 | 22.6 | 1.9 | 52.3 | 0 | 0 | 1009 | -79.3 | Reg closed
GV11 |  | 0.2 | 0.2 | 19.9 | 79.7 | 0 | 0 | 1009 | -76.3 | Reg turned off really bad gas
GV12+R3 |  | 56.5 | 41 | 0.3 | 2.2 | 0 | 0 | 1009 | -79.9 | Left Open Full
GV13 |  | 0.1 | 2 | 18 | 79.9 | 0 | 0 | 1009 | 0.4 | Left Off
GV14 |  | 33.2 | 32.1 | 0.3 | 34.4 | 0 | 5 | 1009 | -77.3 | Reg turned off
GV15 |  | 44.6 | 36.5 | 0.1 | 18.8 | 0 | 3 | 1009 | -77.2 | Left Open Full
GV16 |  | 0.1 | 0.2 | 19.8 | 79.9 | 0 | 0 | 1009 | -30.6 | left off
GV17+LC4 |  | 32 | 18 | 8.7 | 41.3 | 0 | 0 | 1009 | -5.2 | Left off
GV18+21 |  | 42.2 | 37.1 | 0.4 | 20.3 | 0 | 0 | 1009 | -73.4 | reg closed too half way too buld up gas
GV19 |  | 33.4 | 19.9 | 6.6 | 40.1 | 0 | 0 | 1009 | -13.1 | Left Off
GV20 |  | 0.3 | 1 | 19.1 | 79.6 | 0 | 0 | 1009 | 1.4 | Left Off
GV 22 + CVs |  | 0.5 | 3.1 | 17.9 | 78.5 | 0 | 0 | 1009 | 0.69 | Left Off
GV23 |  | 0.1 | 5.6 | 15 | 79.3 | 0 | 0 | 1009 | 0.56 | Left Off
GV24 |  | 44.5 | 39.8 | 0.3 | 15.4 | 0 | 0 | 1009 | -25.74 | Left Open Full
GV25 |  | 47.8 | 34.9 | 0.5 | 16.8 | 0 | 0 | 1009 | -35.69 | Left Open Full
GV26/A |  | 44.5 | 34.1 | 1.4 | 20 | 0 | 0 | 1009 | -33.39 | Left cracked open
GV27+28 / B+C |  | 46.2 | 36.4 | 0.2 | 17.2 | 0 | 0 | 1009 | -31.21 | left open full
GV30 |  | 45 | 35.8 | 0.6 | 18.6 | 0 | 0 | 1009 | -23.63 | Left Open Full
GV31 |  | 51.2 | 40 | 0.2 | 8.6 | 0 | 0 | 1009 | -21.47 | Left Open full
GV32 |  | 30.1 | 30.6 | 1 | 38.3 | 0 | 0 | 1009 | -30.69 | Left off
GV33 |  | 46.3 | 33.5 | 0.5 | 19.7 | 0 | 0 | 1009 | -15.28 | Left cracked open
GV34 |  | 24.1 | 18.9 | 5.9 | 51.1 | 0 | 0 | 1009 | -24.5 | Left closed
RP6.1 |  | 0.2 | 1.2 | 19.9 | 78.7 | 0 | 0 | 1009 | -16 | Left Off
LC1B |  | 0.2 | 0.3 | 19.5 | 80 | 0 | 0 | 1009 | -20.2 | left Off
LC1.1 |  | 54.2 | 2.8 | 0.4 | 42.6 | 0 | 0 | 1009 | -29.97 | Left Open Full
LC2R? |  | 51.2 | 32.4 | 0.2 | 16.2 | 0 | 0 | 1009 | -31.28 | Left Open Full
GV 2.1 |  | 56.3 | 38.9 | 0.3 | 4.5 | 0 | 0 | 1009 | -40.15 | Left Open full
GV 2.2+ LC2B |  | 35.8 | 23 | 2.9 | 38.3 | 0 | 0 | 1009 | -22.03 | Left Off
GV / LC3.1 + LC3 |  | 0.2 | 0.2 | 19.7 | 79.9 | 0 | 0 | 1009 | -33 | Left off
LC4B |  | 26.6 | 25.2 | 5 | 43.2 | 0 | 0 | 1009 | -70.1 | Reg closed.
LC5 |  | 33 | 19.2 | 5.1 | 42.7 | 0 | 0 | 1009 | -12 | Left off
LC6 |  | 32 | 26.8 | 5 | 36.2 | 0 | 0 | 1009 | -7.98 | Left off
GV29D + LC6B |  | 54.1 | 40.8 | 0.4 | 4.7 | 0 | 0 | 1009 | -29.63 | Left Open Full
PW1 |  | 36.3 | 19.9 | 2.5 | 41.3 | 0 | 0 | 1009 | 1.47 | Left Off bad gas high o2
PW2 |  | 40.9 | 16.2 | 0.9 | 42 | 0 | 0 | 1009 | -8.36 | left Cracked Open
PW3 |  | 11.2 | 17.1 | 4 | 67.7 | 0 | 0 | 1009 | 0.23 | Well Left Off
PW4 |  | 28.2 | 13.2 | 3.2 | 55.4 | 0 | 0 | 1009 | 1.02 | left off
PW5 |  | 31.9 | 12.9 | 2.5 | 52.7 | 0 | 0 | 1009 | -0.48 | left off
PW6 |  | 47.1 | 30.2 | 0.3 | 22.4 | 0 | 0 | 1009 | -6.93 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 16:00 | 41.4 | 21.9 | 1 | 35.7 | 4 | 0 | 1009 | -35.69 | Gas improved a lot. Engine 560
Please Note:
Chevrons (>>>) Indicate reading is out of range.

## July
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-07-03
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 19 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0.3 | 1.8 | 19.9 | 78 | 0 | 0 | 995 | 0.42 | 1 | 8.8
BK BH 3 | 10:41 | 0.5 | 1.9 | 20.1 | 77.5 | 0 | 0 | 995 | 0.75 | 1 | 3.1
BK BH 4 | 10:42 | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 995 | 0.41 | 1 | 5.1
BK BH 5 | 10:45 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 995 | 0.59 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 0.6 | 19.1 | 80.3 | 0 | 0 | 995 | -0.23 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 2.5 | 20.3 | 77.2 | 0 | 0 | 995 | 0.14 | 1 | 10
BK BH 8 | 10:55 | 30.6 | 2.1 | 19.9 | 47.4 | 0 | 0 | 995 | -0.53 | 32.2 | 3.6
BK BH 9 | 11:01 | 29.2 | 4.9 | 19.4 | 46.5 | 0 | 0 | 995 | 0.26 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 995 | -0.75 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 2.6 | 20.1 | 77.3 | 0 | 0 | 995 | 0.14 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 1.4 | 20.3 | 78.3 | 0 | 0 | 995 | -0.77 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 995 | 0.56 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 995 | 0.34 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 3.2 | 19.7 | 77.1 | 0 | 0 | 995 | -0.15 | 1 | 17.6
BK BH 16 | 11:35 | 0.6 | 1.2 | 20.1 | 78.1 | 0 | 0 | 995 | 0.26 | 1 | 11.4
BK BH 17 | 11:42 | 0.3 | 1.4 | 20.3 | 78 | 0 | 0 | 995 | 0.31 | 1 | 12.9
BK BH 18 | 10:08 | 1.3 | 2.5 | 20.1 | 76.1 | 0 | 0 | 995 | 0.87 | 6.8 | 21.2
BK BH 19 | 10:12 | 0.6 | 1.8 | 19.2 | 78.4 | 0 | 0 | 995 | 0.9 | 1 | 11.2
BK BH 20 | 10:15 | 0.4 | 4.9 | 20.1 | 74.6 | 0 | 0 | 995 | -0.75 | 1 | 10.7
BK BH 21 | 10:20 | 0.6 | 9.2 | 19.6 | 70.6 | 0 | 0 | 995 | -0.14 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 995 | 0.21 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 995 | 0.68 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1 | 20.3 | 78.7 | 0 | 0 | 995 | -0.71 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-07-10
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:22 | 0.2 | 1.6 | 20 | 78.2 | 0 | 0 | 998 | 0.53 | 1 | 8.8
BK BH 3 | 10:27 | 0.4 | 1 | 19.9 | 78.7 | 0 | 0 | 998 | -0.51 | 1 | 3.1
BK BH 4 | 10:30 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 998 | 0.23 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 998 | 0.47 | 1 | 1.5
BK BH 6 | 10:34 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 998 | 0.57 | 1 | 1.5
BK BH 7 | 10:38 | 0 | 3.2 | 20.1 | 76.7 | 0 | 0 | 998 | 0.53 | 1 | 10
BK BH 8 | 10:41 | 29.8 | 1.2 | 19.6 | 49.4 | 0 | 0 | 998 | 0.48 | 32.2 | 3.6
BK BH 9 | 10:46 | 29 | 4.1 | 19.5 | 47.4 | 0 | 0 | 998 | 0.6 | 29.6 | 10.4
BK BH 10 | 10:52 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 998 | 0.8 | 1 | 3.9
BK BH 11 | 11:04 | 0 | 2.5 | 20.3 | 77.2 | 0 | 0 | 998 | -0.37 | 1 | 6.5
BK BH 12 | 11:08 | 0 | 1 | 20 | 79 | 0 | 0 | 998 | 0.33 | 1 | 6.6
BK BH 13 | 11:12 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 998 | -0.66 | 1 | 9.4
BK BH 14 | 11:15 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 998 | 0.39 | 1 | 3.5
BK BH 15 | 11:18 | 0 | 3 | 20.3 | 76.7 | 0 | 0 | 998 | 0.41 | 1 | 17.6
BK BH 16 | 11:21 | 0.5 | 1.1 | 20.1 | 78.3 | 0 | 0 | 998 | 0.88 | 1 | 11.4
BK BH 17 | 11:28 | 0.3 | 1.2 | 20 | 78.5 | 0 | 0 | 998 | 0.46 | 1 | 12.9
BK BH 18 | 9:54 | 1.4 | 2.3 | 19.5 | 76.8 | 0 | 0 | 998 | -0.42 | 6.8 | 21.2
BK BH 19 | 9:58 | 0.6 | 1.6 | 19.3 | 78.5 | 0 | 0 | 998 | 0.45 | 1 | 11.2
BK BH 20 | 10:01 | 0.4 | 4.9 | 19.8 | 74.9 | 0 | 0 | 998 | 0.57 | 1 | 10.7
BK BH 21 | 10:06 | 0.2 | 8.1 | 19.9 | 71.8 | 0 | 0 | 998 | 0.46 | 1 | 21.7
BK BH 23 | 10:11 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 998 | 0.71 | 1 | 7.3
BK BH 24 | 10:14 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 998 | -0.66 | 1 | 1.5
BK BH 25 | 10:18 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 998 | 0.41 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-07-17
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:58 | 0.2 | 1.6 | 20.1 | 78.1 | 0 | 0 | 1002 | -0.54 | 1 | 8.8
BK BH 3 | 11:03 | 0.3 | 1.5 | 20.3 | 77.9 | 0 | 0 | 1002 | -0.36 | 1 | 3.1
BK BH 4 | 11:04 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1002 | -0.21 | 1 | 5.1
BK BH 5 | 11:06 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | 0.17 | 1 | 1.5
BK BH 6 | 11:10 | 0 | 0.8 | 19.4 | 79.8 | 0 | 0 | 1002 | 0.95 | 1 | 1.5
BK BH 7 | 11:14 | 0 | 2.8 | 20.1 | 77.1 | 0 | 0 | 1002 | -0.63 | 1 | 10
BK BH 8 | 11:17 | 30.2 | 2 | 20.3 | 47.5 | 0 | 0 | 1002 | 0.25 | 32.2 | 3.6
BK BH 9 | 11:23 | 28.7 | 4.2 | 19.6 | 65.9 | 0 | 0 | 1002 | -0.14 | 29.6 | 10.4
BK BH 10 | 11:28 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1002 | 0.25 | 1 | 3.9
BK BH 11 | 11:40 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 1002 | -0.65 | 1 | 6.5
BK BH 12 | 11:44 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1002 | 0.32 | 1 | 6.6
BK BH 13 | 11:48 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | -0.17 | 1 | 9.4
BK BH 14 | 11:51 | 0 | 1 | 19.7 | 79.3 | 0 | 0 | 1002 | 0.36 | 1 | 3.5
BK BH 15 | 11:54 | 0 | 3.5 | 19.8 | 76.7 | 0 | 0 | 1002 | -0.98 | 1 | 17.6
BK BH 16 | 11:57 | 0.5 | 1 | 20 | 78.5 | 0 | 0 | 1002 | 0.25 | 1 | 11.4
BK BH 17 | 12:04 | 0.4 | 1.1 | 20.4 | 78.1 | 0 | 0 | 1002 | -0.11 | 1 | 12.9
BK BH 18 | 10:30 | 1.1 | 2.9 | 19.9 | 76.1 | 0 | 0 | 1002 | 0.75 | 6.8 | 21.2
BK BH 19 | 10:34 | 0.5 | 1.7 | 19.4 | 78.4 | 0 | 0 | 1002 | 0.36 | 1 | 11.2
BK BH 20 | 10:37 | 0.3 | 4.1 | 20.3 | 75.3 | 0 | 0 | 1002 | -0.82 | 1 | 10.7
BK BH 21 | 10:42 | 0.8 | 9.9 | 19.8 | 69.5 | 0 | 0 | 1002 | 0.39 | 1 | 21.7
BK BH 23 | 10:47 | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 1002 | -0.14 | 1 | 7.3
BK BH 24 | 10:50 | 0 | 0.8 | 19.2 | 80 | 0 | 0 | 1002 | 0.27 | 1 | 1.5
BK BH 25 | 10:54 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | -0.54 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-07-24
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 23 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0.3 | 1 | 19.8 | 78.9 | 0 | 0 | 997 | -0.52 | 1 | 8.8
BK BH 3 | 10:28 | 0.5 | 1.3 | 20.1 | 78.1 | 0 | 0 | 997 | -0.12 | 1 | 3.1
BK BH 4 | 10:30 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 997 | 0.32 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 997 | 0.49 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 997 | 0.77 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 997 | 0.52 | 1 | 10
BK BH 8 | 10:42 | 29.9 | 1.8 | 20 | 48.3 | 0 | 0 | 997 | 0.46 | 32.2 | 3.6
BK BH 9 | 10:48 | 29.1 | 3.9 | 19.4 | 47.6 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 997 | 0.36 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 997 | -0.25 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 1.4 | 20.3 | 78.3 | 0 | 0 | 997 | -0.11 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 997 | 0.69 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 997 | 0.75 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 3.2 | 19.4 | 77.4 | 0 | 0 | 997 | -0.11 | 1 | 17.6
BK BH 16 | 11:22 | 0.4 | 0.9 | 19.6 | 79.1 | 0 | 0 | 997 | 0.29 | 1 | 11.4
BK BH 17 | 11:29 | 0.6 | 1.2 | 20.1 | 78.1 | 0 | 0 | 997 | -0.26 | 1 | 12.9
BK BH 18 | 9:55 | 1.2 | 2.4 | 19.5 | 76.9 | 0 | 0 | 997 | 0.52 | 6.8 | 21.2
BK BH 19 | 9:59 | 0.4 | 1.5 | 19.6 | 78.5 | 0 | 0 | 997 | 0.46 | 1 | 11.2
BK BH 20 | 10:02 | 0.5 | 4.4 | 20.4 | 74.7 | 0 | 0 | 997 | -0.68 | 1 | 10.7
BK BH 21 | 10:07 | 0.6 | 9.8 | 19.5 | 70.1 | 0 | 0 | 997 | -0.08 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 997 | 0.21 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 997 | -0.42 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.1 | 20.2 | 78.7 | 0 | 0 | 997 | 0.38 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-07-31
Weather: | Dry
Wind conditions: | breezy
Air Temperature: | 19 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0.2 | 1 | 19.9 | 78.9 | 0 | 0 | 999 | -0.96 | 1 | 8.8
BK BH 3 | 9:51 | 0.4 | 1.3 | 20 | 78.3 | 0 | 0 | 999 | 0.36 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 999 | 0.21 | 1 | 5.1
BK BH 5 | 9:54 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 999 | 0.36 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 999 | 0.87 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 2.5 | 20.1 | 77.4 | 0 | 0 | 999 | 0.53 | 1 | 10
BK BH 8 | 10:05 | 30.2 | 1.8 | 19.7 | 48.3 | 0 | 0 | 999 | 0.26 | 32.2 | 3.6
BK BH 9 | 10:11 | 29.3 | 3.9 | 19.6 | 47.2 | 0 | 0 | 999 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 999 | 0.75 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.5 | 20.2 | 77.3 | 0 | 0 | 999 | 0.21 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 1.4 | 20.3 | 78.3 | 0 | 0 | 999 | -0.44 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 999 | 0.63 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 999 | 0.24 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 3.2 | 19.7 | 77.1 | 0 | 0 | 999 | -0.16 | 1 | 17.6
BK BH 16 | 10:45 | 0.5 | 0.9 | 20.1 | 78.5 | 0 | 0 | 999 | 0.94 | 1 | 11.4
BK BH 17 | 10:52 | 0.4 | 1.2 | 20.3 | 78.1 | 0 | 0 | 999 | 0.87 | 1 | 12.9
BK BH 18 | 9:18 | 1 | 2.4 | 19.6 | 77 | 0 | 0 | 999 | -0.12 | 6.8 | 21.2
BK BH 19 | 9:22 | 0.6 | 1.5 | 19.8 | 78.1 | 0 | 0 | 999 | 0.35 | 1 | 11.2
BK BH 20 | 9:25 | 0.3 | 4.4 | 20.1 | 75.2 | 0 | 0 | 999 | -0.78 | 1 | 10.7
BK BH 21 | 9:30 | 0.8 | 9.8 | 19.6 | 69.8 | 0 | 0 | 999 | 0.63 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 0.4 | 20.3 | 79.3 | 0 | 0 | 999 | 0.25 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 999 | -0.14 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.1 | 20.4 | 78.5 | 0 | 0 | 999 | 0.71 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-07-09
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 24 | oC
Instrument: |  | GEM2000+ | (with H2s filter fitted)
Serial No: |  | GH12289/10
Calibrated To: |  | 2014-08-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 9:40 | 37.2 | 30.4 | 1.8 | 30.6 | 1 | 0 | 1002 | -40.21
GV1 |  | 1 | 0.8 | 18.4 | 79.8 | 0 | 0 | 1002 | -13.28 | left Off
GV2 |  | 50.2 | 32.8 | 0.3 | 16.7 | 0 | 0 | 1002 | -31.98 | Left Open full
GV3 |  | 61.3 | 30.9 | 0.2 | 7.6 | 0 | 0 | 1002 | 0.01 | Left Open full
GV4 |  | 31.8 | 29.6 | 0.7 | 37.9 | 0 | 0 | 1002 | -0.58 | Left Off bad gas
GV5+R1 |  | 40.2 | 30.2 | 5.1 | 24.5 | 0 | 0 | 1002 | -0.14 | Left Off bad gas, high o2
GV6 |  | 54.8 | 30.9 | 0.3 | 14 | 0 | 0 | 1002 | -32.59 | Left Open Full
GV7 |  | 47.1 | 31.1 | 1 | 20.8 | 0 | 0 | 1002 | -21.39 | Left cracked open
GV8 |  | 27 | 23 | 3.2 | 46.8 | 3 | 0 | 1002 | 2.14 | Left Off
GV9 |  | 50 | 33.9 | 0.4 | 15.7 | 0 | 0 | 1002 | -60.29 | Left Open Full
GV9.1 |  | 0.7 | 0.4 | 20 | 78.9 | 0 | 0 | 1002 | 0.89 | left off
GV10 |  | 45.9 | 24 | 0.9 | 29.2 | 0 | 0 | 1002 | -21.14 | Reg cracked open good gas
GV11 |  | 0.3 | 0.9 | 19.6 | 79.2 | 0 | 0 | 1002 | 0.28 | Left turned off
GV12+R3 |  | 54.1 | 40.2 | 0.4 | 5.3 | 0 | 0 | 1002 | 55.87 | Left Open Full
GV13 |  | 0.4 | 2.3 | 19.9 | 77.4 | 0 | 0 | 1002 | 0.41 | Left Off
GV14 |  | 35.2 | 30.7 | 0.4 | 33.7 | 0 | 7 | 1002 | 0.23 | Left turned off
GV15 |  | 49.9 | 31.1 | 0.3 | 18.7 | 0 | 1 | 1002 | -69.31 | Left Open Full
GV16 |  | 0.2 | 0.6 | 20 | 79.2 | 0 | 0 | 1002 | 0.23 | left off
GV17+LC4 |  | 33.6 | 18.4 | 9.7 | 38.3 | 0 | 0 | 1002 | -0.89 | Left off
GV18+21 |  | 46.8 | 35.1 | 0.5 | 17.6 | 0 | 0 | 1002 | -54.12 | reg opened full good gas
GV19 |  | 30.2 | 20.1 | 7 | 42.7 | 0 | 0 | 1002 | 0.23 | Left Off
GV20 |  | 0.6 | 1.4 | 18.5 | 79.5 | 0 | 0 | 1002 | 1.21 | Left Off
GV 22 + CVs |  | 0.9 | 3.5 | 18.3 | 77.3 | 0 | 0 | 1002 | 0.89 | Left Off
GV23 |  | 1.2 | 6 | 16.9 | 75.9 | 0 | 0 | 1002 | -0.12 | Left Off
GV24 |  | 46.3 | 36 | 0.4 | 17.3 | 0 | 0 | 1002 | -40.28 | Left Open Full
GV25 |  | 49.2 | 33.6 | 0.6 | 16.6 | 0 | 0 | 1002 | -38.24 | Left Open Full
GV26/A |  | 45.2 | 32.1 | 1 | 21.7 | 0 | 0 | 1002 | -17.03 | Left cracked open
GV27+28 / B+C |  | 45.2 | 35.8 | 0.3 | 18.7 | 0 | 0 | 1002 | -32.98 | left open full
GV30 |  | 47.9 | 34.1 | 0.5 | 17.5 | 0 | 0 | 1002 | -39.21 | Left Open Full
GV31 |  | 50.3 | 39.6 | 0.3 | 9.8 | 0 | 0 | 1002 | -30.88 | Left Open full
GV32 |  | 35.9 | 29.6 | 1.1 | 33.4 | 0 | 0 | 1002 | -0.39 | Left off
GV33 |  | 44.5 | 32.5 | 0.9 | 22.1 | 0 | 0 | 1002 | -17.48 | Left cracked open
GV34 |  | 21.3 | 17.8 | 6 | 54.9 | 0 | 0 | 1002 | 0.21 | Left closed
RP6.1 |  | 0.3 | 1.8 | 20 | 77.9 | 0 | 0 | 1002 | 0.23 | Left Off
LC1B |  | 0.9 | 0.4 | 19.1 | 79.6 | 0 | 0 | 1002 | 0.99 | left Off
LC1.1 |  | 55.6 | 22.2 | 0.6 | 21.6 | 0 | 0 | 1002 | -35.66 | Left Open Full
LC2R? |  | 54.1 | 33.6 | 0.7 | 11.6 | 0 | 0 | 1002 | -40.12 | Left Open Full
GV 2.1 |  | 55.2 | 38.1 | 0.8 | 5.9 | 0 | 0 | 1002 | -39.57 | Left Open full
GV 2.2+ LC2B |  | 31.2 | 22.7 | 2.2 | 43.9 | 0 | 0 | 1002 | 0.21 | Left Off
GV / LC3.1 + LC3 |  | 0.9 | 0.4 | 19.2 | 79.5 | 0 | 0 | 1002 | 0.39 | Left off
LC4B |  | 48.1 | 26.9 | 1 | 24 | 0 | 0 | 1002 | -21.93 | Reg cracked open good gas
LC5 |  | 32 | 20 | 4.8 | 43.2 | 0 | 0 | 1002 | 0.21 | Left off
LC6 |  | 33.9 | 27.8 | 4.1 | 34.2 | 0 | 0 | 1002 | 0.39 | Left off
GV29D + LC6B |  | 53.6 | 41.2 | 0.5 | 4.7 | 0 | 0 | 1002 | -38.52 | Left Open Full
PW1 |  | 38.1 | 20.1 | 2.1 | 39.7 | 0 | 0 | 1002 | 1 | Left Off bad gas high o2
PW2 |  | 44.9 | 17.5 | 1.1 | 36.5 | 0 | 0 | 1002 | -11.14 | left Cracked Open
PW3 |  | 17.8 | 15.6 | 3.2 | 63.4 | 0 | 0 | 1002 | 0.66 | turned off bad gas
PW4 |  | 30.2 | 17.4 | 3 | 49.4 | 0 | 0 | 1002 | 0.21 | left off
PW5 |  | 35.9 | 13.8 | 4.5 | 45.8 | 0 | 0 | 1002 | -0.02 | left off
PW6 |  | 48.9 | 31.2 | 0.4 | 19.5 | 0 | 0 | 1002 | -22.9 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 15:35 | 40.1 | 29.9 | 1 | 29 | 2 | 0 | 1002 | -38.24 | Gas improved slightly. Engine 560

## August
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-08-07
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:22 | 0.3 | 0.9 | 20.1 | 78.7 | 0 | 0 | 998 | -0.52 | 1 | 8.8
BK BH 3 | 10:27 | 0.5 | 1.2 | 20.2 | 78.1 | 0 | 0 | 998 | 0.52 | 1 | 3.1
BK BH 4 | 10:29 | 0 | 0.7 | 19.5 | 79.8 | 0 | 0 | 998 | 0.45 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.9 | 19.1 | 80 | 0 | 0 | 998 | 0.32 | 1 | 1.5
BK BH 6 | 10:34 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 998 | 0.32 | 1 | 1.5
BK BH 7 | 10:38 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 998 | 0.42 | 1 | 10
BK BH 8 | 10:41 | 29.9 | 1.2 | 19.6 | 49.3 | 0 | 0 | 998 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:46 | 29 | 3.5 | 19.2 | 48.3 | 0 | 0 | 998 | 0.25 | 29.6 | 10.4
BK BH 10 | 10:52 | 0 | 1.9 | 19.1 | 79 | 0 | 0 | 998 | -0.14 | 1 | 3.9
BK BH 11 | 11:04 | 0 | 2.9 | 20.4 | 76.7 | 0 | 0 | 998 | 0.75 | 1 | 6.5
BK BH 12 | 11:08 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 998 | -0.63 | 1 | 6.6
BK BH 13 | 11:12 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 998 | -0.25 | 1 | 9.4
BK BH 14 | 11:15 | 0 | 1.4 | 20.8 | 77.8 | 0 | 0 | 998 | 0.24 | 1 | 3.5
BK BH 15 | 11:18 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 998 | 0.69 | 1 | 17.6
BK BH 16 | 11:21 | 0.4 | 1.1 | 20.4 | 78.1 | 0 | 0 | 998 | -0.15 | 1 | 11.4
BK BH 17 | 11:28 | 0.6 | 1.5 | 20.3 | 77.6 | 0 | 0 | 998 | -0.42 | 1 | 12.9
BK BH 18 | 9:54 | 0.9 | 2 | 19.9 | 77.2 | 0 | 0 | 998 | -0.11 | 6.8 | 21.2
BK BH 19 | 9:58 | 0.5 | 1.2 | 20.1 | 78.2 | 0 | 0 | 998 | 0.89 | 1 | 11.2
BK BH 20 | 10:01 | 0.4 | 4.1 | 20.4 | 75.1 | 0 | 0 | 998 | -0.72 | 1 | 10.7
BK BH 21 | 10:06 | 0.7 | 9.2 | 19.9 | 70.2 | 0 | 0 | 998 | 0.58 | 1 | 21.7
BK BH 23 | 10:11 | 0 | 0.4 | 20.3 | 79.3 | 0 | 0 | 998 | 0.71 | 1 | 7.3
BK BH 24 | 10:14 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 998 | 0.74 | 1 | 1.5
BK BH 25 | 10:18 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 998 | -0.17 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-08-14
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 20 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:52 | 0.2 | 0.6 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.72 | 1 | 8.8
BK BH 3 | 11:57 | 0.4 | 1 | 20.3 | 78.3 | 0 | 0 | 1002 | -0.48 | 1 | 3.1
BK BH 4 | 11:59 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 1002 | 0.58 | 1 | 5.1
BK BH 5 | 12:01 | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1002 | 0.61 | 1 | 1.5
BK BH 6 | 12:04 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 1002 | 0.72 | 1 | 1.5
BK BH 7 | 12:08 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1002 | 0.84 | 1 | 10
BK BH 8 | 12:11 | 30.1 | 1.1 | 19.8 | 49 | 0 | 0 | 1002 | 0.63 | 32.2 | 3.6
BK BH 9 | 12:17 | 28.6 | 3.2 | 19.5 | 48.7 | 0 | 0 | 1002 | 0.78 | 29.6 | 10.4
BK BH 10 | 12:22 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 1002 | 0.78 | 1 | 3.9
BK BH 11 | 12:34 | 0 | 2.5 | 20.1 | 77.4 | 0 | 0 | 1002 | -0.62 | 1 | 6.5
BK BH 12 | 12:38 | 0 | 0.8 | 20.3 | 78.9 | 0 | 0 | 1002 | 0.47 | 1 | 6.6
BK BH 13 | 12:42 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1002 | -0.97 | 1 | 9.4
BK BH 14 | 12:45 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1002 | 0.41 | 1 | 3.5
BK BH 15 | 12:48 | 0 | 2.6 | 19.2 | 78.2 | 0 | 0 | 1002 | 0.56 | 1 | 17.6
BK BH 16 | 12:51 | 0.3 | 0.9 | 20.3 | 78.5 | 0 | 0 | 1002 | 1.27 | 1 | 11.4
BK BH 17 | 12:58 | 0.2 | 1.2 | 20 | 78.6 | 0 | 0 | 1002 | 0.89 | 1 | 12.9
BK BH 18 | 11:24 | 0.8 | 2.1 | 19.8 | 77.3 | 0 | 0 | 1002 | 0.59 | 6.8 | 21.2
BK BH 19 | 11:28 | 0.6 | 1.4 | 19.6 | 78.4 | 0 | 0 | 1002 | 0.78 | 1 | 11.2
BK BH 20 | 11:31 | 0.3 | 4.5 | 20.1 | 75.1 | 0 | 0 | 1002 | 0.5 | 1 | 10.7
BK BH 21 | 11:36 | 0.6 | 9.5 | 19.8 | 70.1 | 0 | 0 | 1002 | 0.56 | 1 | 21.7
BK BH 23 | 11:41 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1002 | 0.82 | 1 | 7.3
BK BH 24 | 11:44 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1002 | -0.89 | 1 | 1.5
BK BH 25 | 11:48 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-08-21
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM2000+
Serial No: | GH12289/10
Calibrated To: | 2014-08-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0.3 | 0.9 | 19.8 | 79 | 0 | 0 | 999 | -0.56 | 1 | 8.8
BK BH 3 | 9:51 | 0.3 | 1.3 | 20.1 | 78.3 | 0 | 0 | 999 | 0.42 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 999 | 0.32 | 1 | 5.1
BK BH 5 | 9:54 | 0 | 0.8 | 19.1 | 80.1 | 0 | 0 | 999 | -0.21 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 999 | -0.15 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 999 | 0.36 | 1 | 10
BK BH 8 | 10:05 | 29.9 | 1 | 19.5 | 49.6 | 0 | 0 | 999 | -0.47 | 32.2 | 3.6
BK BH 9 | 10:11 | 28.9 | 2.9 | 19.2 | 49 | 0 | 0 | 999 | 0.96 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.52 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 999 | -0.15 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 999 | 0.36 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 0.8 | 19.2 | 80 | 0 | 0 | 999 | -0.42 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 0.9 | 20.3 | 78.8 | 0 | 0 | 999 | 0.18 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 999 | -0.63 | 1 | 17.6
BK BH 16 | 10:45 | 0.2 | 0.8 | 20.1 | 78.9 | 0 | 0 | 999 | 0.14 | 1 | 11.4
BK BH 17 | 10:52 | 0.4 | 1.4 | 19.6 | 78.6 | 0 | 0 | 999 | 0.75 | 1 | 12.9
BK BH 18 | 9:18 | 0.6 | 2 | 19.5 | 77.9 | 0 | 0 | 999 | -0.86 | 6.8 | 21.2
BK BH 19 | 9:22 | 0.5 | 1.2 | 19.2 | 79.1 | 0 | 0 | 999 | 0.35 | 1 | 11.2
BK BH 20 | 9:25 | 0.4 | 4.9 | 19.6 | 75.1 | 0 | 0 | 999 | -0.77 | 1 | 10.7
BK BH 21 | 9:30 | 0.8 | 9.2 | 19.5 | 70.5 | 0 | 0 | 999 | -0.86 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 0.9 | 20.2 | 78.9 | 0 | 0 | 999 | -0.12 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 1.1 | 19.4 | 79.5 | 0 | 0 | 999 | 0.48 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 999 | 0.47 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-08-28
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 22 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:06 | 0.2 | 0.8 | 19.9 | 79.1 | 0 | 0 | 997 | -0.36 | 1 | 8.8
BK BH 3 | 10:11 | 0.1 | 1.2 | 20.3 | 78.4 | 0 | 0 | 997 | 0.25 | 1 | 3.1
BK BH 4 | 10:12 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 997 | -0.12 | 1 | 5.1
BK BH 5 | 10:14 | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 997 | 0.47 | 1 | 1.5
BK BH 6 | 10:18 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 997 | 0.18 | 1 | 1.5
BK BH 7 | 10:22 | 0 | 1.8 | 19.6 | 78.6 | 0 | 0 | 997 | -0.52 | 1 | 10
BK BH 8 | 10:25 | 29.2 | 1.2 | 19.2 | 50.4 | 0 | 0 | 997 | 0.65 | 32.2 | 3.6
BK BH 9 | 10:31 | 28.1 | 2.5 | 19.9 | 49.5 | 0 | 0 | 997 | 0.78 | 29.6 | 10.4
BK BH 10 | 10:36 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 997 | -0.23 | 1 | 3.9
BK BH 11 | 10:48 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 997 | 0.64 | 1 | 6.5
BK BH 12 | 10:52 | 0 | 0.9 | 20.3 | 78.8 | 0 | 0 | 997 | 0.57 | 1 | 6.6
BK BH 13 | 10:56 | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 997 | -0.11 | 1 | 9.4
BK BH 14 | 10:59 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 997 | 0.54 | 1 | 3.5
BK BH 15 | 11:02 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.84 | 1 | 17.6
BK BH 16 | 11:05 | 0.3 | 0.6 | 20.2 | 78.9 | 0 | 0 | 997 | -0.11 | 1 | 11.4
BK BH 17 | 11:12 | 0.1 | 1.2 | 20.1 | 78.6 | 0 | 0 | 997 | 0.36 | 1 | 12.9
BK BH 18 | 9:38 | 0.5 | 2.3 | 19.9 | 77.3 | 0 | 0 | 997 | 0.58 | 6.8 | 21.2
BK BH 19 | 9:42 | 0.6 | 1 | 19.5 | 78.9 | 0 | 0 | 997 | 0.47 | 1 | 11.2
BK BH 20 | 9:45 | 0.2 | 4.5 | 19.8 | 75.5 | 0 | 0 | 997 | -0.25 | 1 | 10.7
BK BH 21 | 9:50 | 0.5 | 8.6 | 19.9 | 71 | 0 | 0 | 997 | 0.79 | 1 | 21.7
BK BH 23 | 9:55 | 0 | 0.5 | 20.1 | 79.4 | 0 | 0 | 997 | 0.28 | 1 | 7.3
BK BH 24 | 9:58 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 997 | -0.2 | 1 | 1.5
BK BH 25 | 10:02 | 0 | 1.2 | 19.2 | 79.6 | 0 | 0 | 997 | -0.11 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-08-29
Weather: |  | Dry/Overcast
Wind conditions: |  | Calm
Air Temperature: |  | 21 | oC
Instrument: |  | GA2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2015-02-18
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 9:30 | 39.6 | 30.2 | 1.5 | 28.7 | 2 | 0 | 1002
GV1 |  | 1.2 | 1.5 | 14.2 | 83.1 | 0 | 0 | 1002 | 0.22 | left Off
GV2 |  | 40.2 | 31.9 | 0.6 | 27.3 | 0 | 0 | 1002 | -36.98 | Left Open full
GV3 |  | 57.1 | 29.6 | 0.3 | 13 | 0 | 0 | 1002 | -30.24 | Left Open full
GV4 |  | 36.3 | 25.2 | 1.2 | 37.3 | 0 | 0 | 1002 | 0.14 | Left Off bad gas
GV5+R1 |  | 41.5 | 30.9 | 3.1 | 24.5 | 0 | 0 | 1002 | 0.25 | Left Off bad gas, high o2
GV6 |  | 51.2 | 28.5 | 0.4 | 19.9 | 1 | 0 | 1002 | -32.69 | Left Open Full
GV7 |  | 46.8 | 29.6 | 1 | 22.6 | 0 | 0 | 1002 | -12.45 | Left cracked open
GV8 |  | 29.6 | 21.4 | 3.2 | 45.8 | 3 | 0 | 1002 | 3.25 | Left Off
GV9 |  | 50.8 | 31.6 | 0.5 | 17.1 | 0 | 0 | 1002 | -40.18 | Left Open Full
GV9.1 |  | 0.7 | 0.4 | 19.5 | 79.4 | 0 | 0 | 1002 | 0.52 | left off
GV10 |  | 44.5 | 19.8 | 4.1 | 31.6 | 0 | 0 | 1002 | 0.21 | Reg closed high o2
GV11 |  | 45.8 | 15.2 | 2.9 | 36.1 | 0 | 0 | 1002 | 0.98 | Reg closed high o2
GV12+R3 |  | 50.1 | 42.6 | 0.9 | 6.4 | 0 | 0 | 1002 | -33.69 | Left Open Full
GV13 |  | 0.8 | 2.1 | 17.8 | 79.3 | 0 | 0 | 1002 | 0.41 | Left Off
GV14 |  | 30.2 | 29.8 | 0.5 | 39.5 | 0 | 7 | 1002 | 0.59 | Left turned off
GV15 |  | 52.1 | 28.7 | 0.1 | 19.1 | 0 | 2 | 1002 | -36.92 | Left Open Full
GV16 |  | 0.5 | 0.9 | 18.5 | 80.1 | 0 | 0 | 1002 | 0.33 | left off
GV17+LC4 |  | 35.2 | 15.7 | 9 | 40.1 | 0 | 0 | 1002 | 0.47 | Left off
GV18+21 |  | 47.2 | 33.8 | 0.4 | 18.6 | 0 | 0 | 1002 | -40.15 | Left Open full
GV19 |  | 17.2 | 15.8 | 6.9 | 60.1 | 0 | 0 | 1002 | 0.41 | Left Off
GV20 |  | 0.2 | 1.6 | 17.5 | 80.7 | 0 | 0 | 1002 | 0.98 | Left Off
GV 22 + CVs |  | 1 | 3 | 17.3 | 78.7 | 0 | 0 | 1002 | 0.48 | Left Off
GV23 |  | 1.2 | 5.9 | 16.9 | 76 | 0 | 0 | 1002 | -0.01 | Left Off
GV24 |  | 51.2 | 33.6 | 0.6 | 14.6 | 0 | 8 | 1002 | -30.25 | Left Open Full
GV25 |  | 45 | 31.8 | 0.7 | 22.5 | 0 | 4 | 1002 | -27.58 | Left Open Full
GV26/A |  | 48.9 | 32.7 | 0.9 | 17.5 | 0 | 8 | 1002 | -22.33 | Reg opened half way good gas
GV27+28 / B+C |  | 46.9 | 30.2 | 0.3 | 22.6 | 0 | 0 | 1002 | -31.78 | left open full
GV30 |  | 45.2 | 31.8 | 0.5 | 22.5 | 0 | 0 | 1002 | -35.69 | Left Open Full
GV31 |  | 49.3 | 36.5 | 0.4 | 13.8 | 0 | 0 | 1002 | -30.14 | Left Open full
GV32 |  | 42.2 | 29.8 | 1 | 27 | 0 | 0 | 1002 | -5.69 | reg cracked open
GV33 |  | 40.2 | 29.7 | 1.1 | 29 | 0 | 0 | 1002 | -8.96 | Left cracked open
GV34 |  | 41.5 | 19.8 | 1.2 | 37.5 | 0 | 0 | 1002 | 0.15 | Reg cracked open
RP6.1 |  | 0.3 | 2.1 | 19.2 | 78.4 | 0 | 0 | 1002 | 0.23 | Left Off
LC1B |  | 0.9 | 0.4 | 9.9 | 88.8 | 0 | 0 | 1002 | 0.52 | left Off
LC1.1 |  | 52.1 | 19.9 | 0.4 | 27.6 | 0 | 0 | 1002 | -36.99 | Left Open Full
LC2R? |  | 49.6 | 33.6 | 1 | 15.8 | 0 | 0 | 1002 | -8.92 | Reg closed too cracked
GV 2.1 |  | 49.6 | 36.5 | 0.4 | 13.5 | 0 | 0 | 1002 | -35.21 | Left Open full
GV 2.2+ LC2B |  | 43.8 | 21.8 | 1.1 | 33.3 | 0 | 0 | 1002 | -8.04 | reg cracked open
GV / LC3.1 + LC3 |  | 16.3 | 0.9 | 17.2 | 65.6 | 0 | 0 | 1002 | 0.45 | Left off
LC4B |  | 48.7 | 22.1 | 0.9 | 28.3 | 0 | 0 | 1002 | -25.69 | Fixed headworks, (Gas leak) opened half way.
LC5 |  | 41.2 | 20.3 | 3.1 | 35.4 | 0 | 0 | 1002 | 0.69 | Left off
LC6 |  | 49.9 | 24.2 | 0.7 | 25.2 | 0 | 0 | 1002 | -6.52 | Reg cracked open good gas.
GV29D + LC6B |  | 51.2 | 38.7 | 0.7 | 9.4 | 0 | 0 | 1002 | -30.36 | Left Open Full
PW1 |  | 39.9 | 22.6 | 2.5 | 35 | 0 | 0 | 1002 | 0.24 | Left Off bad gas high o2
PW2 |  | 48.2 | 18.2 | 1.1 | 32.5 | 0 | 0 | 1002 | -8.21 | left Cracked Open
PW3 |  | 18.2 | 15.4 | 3.6 | 62.8 | 0 | 0 | 1002 | 0.36 | left off
PW4 |  | 33.6 | 18.9 | 2.9 | 44.6 | 0 | 0 | 1002 | 0.89 | left off
PW5 |  | 38.4 | 12.2 | 3.2 | 46.2 | 0 | 0 | 1002 | 0.41 | left off
PW6 |  | 48.2 | 29.9 | 0.4 | 21.5 | 0 | 0 | 1002 | -30.69 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 14:00 | 43.2 | 31.2 | 1.1 | 24.5 | 4 | 0 | 1002 |  | Gas improved slightly. Engine 520
Please Note:
Chevrons (>>>) Indicate reading is out of range.

## September
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-09-04
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 18 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0.3 | 0.6 | 20.1 | 79 | 0 | 0 | 998 | 0.49 | 1 | 8.8
BK BH 3 | 10:41 | 0.4 | 1 | 20.1 | 78.5 | 0 | 0 | 998 | -0.62 | 1 | 3.1
BK BH 4 | 10:43 | 0 | 0.2 | 19.9 | 79.9 | 0 | 0 | 998 | 0.42 | 1 | 5.1
BK BH 5 | 10:45 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 998 | -0.32 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 998 | 0.75 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 998 | 0.36 | 1 | 10
BK BH 8 | 10:55 | 29.5 | 1.4 | 19.8 | 49.3 | 0 | 0 | 998 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:01 | 28.5 | 2.1 | 19.5 | 49.9 | 0 | 0 | 998 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | 0.69 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 998 | -0.15 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 998 | 0.24 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 998 | -0.63 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 0.6 | 20.3 | 79.1 | 0 | 0 | 998 | 0.21 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 998 | 0.02 | 1 | 17.6
BK BH 16 | 11:35 | 0.5 | 0.8 | 20.1 | 78.6 | 0 | 0 | 998 | 0.58 | 1 | 11.4
BK BH 17 | 11:42 | 0.4 | 1.2 | 20.3 | 78.1 | 0 | 0 | 998 | 0.77 | 1 | 12.9
BK BH 18 | 10:08 | 0.2 | 2.4 | 19.4 | 78 | 0 | 0 | 998 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:12 | 0.8 | 1.2 | 19.6 | 78.4 | 0 | 0 | 998 | 0.38 | 1 | 11.2
BK BH 20 | 10:15 | 0.4 | 4.9 | 19.7 | 75 | 0 | 0 | 998 | -0.25 | 1 | 10.7
BK BH 21 | 10:20 | 0.8 | 8.2 | 19.8 | 71.2 | 0 | 0 | 998 | 0.14 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 0.6 | 20.3 | 79.1 | 0 | 0 | 998 | 0.75 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 998 | -0.63 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 998 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-09-11
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:45 | 0.2 | 0.8 | 19.9 | 79.1 | 0 | 0 | 1003 | -0.63 | 1 | 8.8
BK BH 3 | 10:50 | 0.5 | 1.2 | 19.7 | 78.6 | 0 | 0 | 1003 | -0.25 | 1 | 3.1
BK BH 4 | 10:51 | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1003 | -0.35 | 1 | 5.1
BK BH 5 | 10:53 | 0 | 1.1 | 20.3 | 78.6 | 0 | 0 | 1003 | 0.47 | 1 | 1.5
BK BH 6 | 10:57 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1003 | -0.65 | 1 | 1.5
BK BH 7 | 11:01 | 0 | 1.2 | 20.2 | 78.6 | 0 | 0 | 1003 | 0.35 | 1 | 10
BK BH 8 | 11:04 | 29.2 | 1.7 | 19.5 | 49.6 | 0 | 0 | 1003 | -0.14 | 32.2 | 3.6
BK BH 9 | 11:10 | 29 | 2.3 | 19.6 | 49.1 | 0 | 0 | 1003 | 0.25 | 29.6 | 10.4
BK BH 10 | 11:15 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1003 | 0.38 | 1 | 3.9
BK BH 11 | 11:27 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1003 | -0.96 | 1 | 6.5
BK BH 12 | 11:31 | 0 | 0.7 | 20.3 | 79 | 0 | 0 | 1003 | 0.15 | 1 | 6.6
BK BH 13 | 11:35 | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1003 | 0.24 | 1 | 9.4
BK BH 14 | 11:38 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 1003 | -0.75 | 1 | 3.5
BK BH 15 | 11:41 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 1003 | 0.38 | 1 | 17.6
BK BH 16 | 11:44 | 0.4 | 0.6 | 19.7 | 79.3 | 0 | 0 | 1003 | -0.77 | 1 | 11.4
BK BH 17 | 11:51 | 0.6 | 0.9 | 19.6 | 78.9 | 0 | 0 | 1003 | -0.65 | 1 | 12.9
BK BH 18 | 10:17 | 0.3 | 2.1 | 19.5 | 78.1 | 0 | 0 | 1003 | -78 | 6.8 | 21.2
BK BH 19 | 10:21 | 0.6 | 1.3 | 19.8 | 78.3 | 0 | 0 | 1003 | 0.63 | 1 | 11.2
BK BH 20 | 10:24 | 0.5 | 5.2 | 20.1 | 74.2 | 0 | 0 | 1003 | -0.87 | 1 | 10.7
BK BH 21 | 10:29 | 0.7 | 7.9 | 19.9 | 71.5 | 0 | 0 | 1003 | -0.58 | 1 | 21.7
BK BH 23 | 10:34 | 0 | 0.5 | 20.1 | 79.4 | 0 | 0 | 1003 | -0.48 | 1 | 7.3
BK BH 24 | 10:37 | 0 | 0.7 | 20.3 | 79 | 0 | 0 | 1003 | -0.25 | 1 | 1.5
BK BH 25 | 10:41 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1003 | 0.86 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-09-18
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 17 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0.3 | 0.5 | 20.2 | 79 | 0 | 0 | 998 | -0.52 | 1 | 8.8
BK BH 3 | 10:28 | 0.4 | 1.1 | 19.5 | 79 | 0 | 0 | 998 | -0.12 | 1 | 3.1
BK BH 4 | 10:29 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 998 | -0.19 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 998 | 0.23 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 998 | 0.77 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 998 | 0.52 | 1 | 10
BK BH 8 | 10:42 | 28.2 | 1.2 | 19.6 | 51 | 0 | 0 | 998 | 0.46 | 32.2 | 3.6
BK BH 9 | 10:48 | 28.9 | 2.1 | 19.9 | 49.1 | 0 | 0 | 998 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 998 | 0.36 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 998 | -0.25 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 998 | -0.11 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 998 | 0.69 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 998 | 0.75 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 998 | -0.11 | 1 | 17.6
BK BH 16 | 11:22 | 0.5 | 0.8 | 19.9 | 78.8 | 0 | 0 | 998 | 0.29 | 1 | 11.4
BK BH 17 | 11:29 | 0.4 | 1.1 | 20.1 | 78.4 | 0 | 0 | 998 | -0.26 | 1 | 12.9
BK BH 18 | 9:55 | 0.2 | 2.3 | 19.4 | 78.1 | 0 | 0 | 998 | 0.52 | 6.8 | 21.2
BK BH 19 | 9:59 | 0.7 | 1.2 | 19.6 | 78.5 | 0 | 0 | 998 | 0.46 | 1 | 11.2
BK BH 20 | 10:02 | 0.3 | 5.1 | 20.3 | 74.3 | 0 | 0 | 998 | -0.68 | 1 | 10.7
BK BH 21 | 10:07 | 0.5 | 7.8 | 19.6 | 72.1 | 0 | 0 | 998 | -0.08 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 998 | 0.21 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 998 | -0.42 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 998 | 0.38 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-09-25
Weather: | slight rain
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0.2 | 0.6 | 19.9 | 79.3 | 0 | 0 | 998 | -0.54 | 1 | 8.8
BK BH 3 | 10:08 | 0.5 | 1 | 19.4 | 79.1 | 0 | 0 | 998 | 0.38 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 998 | 0.48 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 0.6 | 20.2 | 79.2 | 0 | 0 | 998 | -0.58 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 998 | 0.21 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 1.4 | 20.3 | 78.3 | 0 | 0 | 998 | 0.36 | 1 | 10
BK BH 8 | 10:22 | 28.5 | 1 | 19.8 | 50.7 | 0 | 0 | 998 | 0.58 | 32.2 | 3.6
BK BH 9 | 10:28 | 28.4 | 1.9 | 20.1 | 49.6 | 0 | 0 | 998 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | 0.68 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 998 | 0.87 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 998 | 0.59 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 998 | 0.23 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1 | 19.2 | 79.8 | 0 | 0 | 998 | 0.87 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 998 | -0.15 | 1 | 17.6
BK BH 16 | 11:02 | 0.4 | 0.9 | 20.1 | 78.6 | 0 | 0 | 998 | 0.23 | 1 | 11.4
BK BH 17 | 11:09 | 0.6 | 1 | 20.3 | 78.1 | 0 | 0 | 998 | -0.46 | 1 | 12.9
BK BH 18 | 9:35 | 0.3 | 2.1 | 19.6 | 78 | 0 | 0 | 998 | 0.68 | 6.8 | 21.2
BK BH 19 | 9:39 | 0.5 | 1.4 | 19.2 | 78.9 | 0 | 0 | 998 | 0.78 | 1 | 11.2
BK BH 20 | 9:42 | 0.4 | 5.2 | 20.1 | 74.3 | 0 | 0 | 998 | -0.15 | 1 | 10.7
BK BH 21 | 9:47 | 0.6 | 7.2 | 19.8 | 72.4 | 0 | 0 | 998 | 0.24 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 998 | 0.25 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 0.8 | 20.3 | 78.9 | 0 | 0 | 998 | -0.78 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 998 | 0.52 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-09-10
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 18 | oC
Instrument: |  | GA2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2015-02-18
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 10:00 | 42.3 | 35.9 | 0.8 | 21 | 7 | 0 | 1006 | 166
GV1 |  | 0.5 | 1 | 10.9 | 87.6 | 0 | 1 | 1006 | 0.1 | left Off
GV2 |  | 10 | 21.5 | 1.1 | 67.4 | 8 | 4 | 1006 | -44.2 | Reg Closeed
GV3 |  | 59.4 | 36 | 0.4 | 4.2 | 6 | 0 | 1006 | -32.86 | Left Open full
GV4 |  | 47 | 30.2 | 0.8 | 22 | 6 | 0 | 1006 | -5.21 | Reg Cracked Open
GV5+R1 |  | 50.8 | 29.2 | 5.1 | 14.9 | 0 | 0 | 1006 | 0.01 | Left Off high o2
GV6 |  | 49.5 | 34.7 | 0.5 | 15.3 | 6 | 0 | 1006 | -39.8 | Left Open Full
GV7 |  | 39.2 | 27.1 | 3.9 | 29.8 | 0 | 0 | 1006 | -19.24 | Reg Closed
GV8 |  | 35 | 22.2 | 4.6 | 38.2 | 7 | 0 | 1006 | 0.1 | Left Off
GV9 |  | 59.7 | 37.5 | 0.3 | 2.5 | 8 | 0 | 1006 | -44.73 | Left Open Full
GV9.1 |  | 0.4 | 0.8 | 20.4 | 78.4 | 0 | 0 | 1006 | 0.02 | left off
GV10 |  | 65.1 | 34.1 | 0.3 | 0.5 | 1 | 0 | 1006 | -4.21 | Reg Cracked open
GV11 |  | 60.5 | 39.5 | 0.2 | -0.2 | 3 | 0 | 1006 | -5.21 | Reg cracked open good gas
GV12+R3 |  | 52.5 | 35.5 | 1.9 | 10.1 | 12 | 0 | 1006 | -23 | Left Open Full
GV13 |  | 0.3 | 1.7 | 17.4 | 80.6 | 0 | 0 | 1006 | 0 | Left Off
GV14 |  | 20.1 | 11.1 | 0.8 | 68 | 1 | 5 | 1006 | -0.15 | Left turned off
GV15 |  | 56.5 | 41 | 0.3 | 2.2 | 16 | 2 | 1006 | -48.05 | Left Open Full
GV16 |  | 13.9 | 7 | 14.9 | 64.2 | 1 | 0 | 1006 | 0.12 | left off
GV17+LC4 |  | 39.9 | 28.4 | 5.4 | 26.3 | 5 | 0 | 1006 | 0 | Left off
GV18+21 |  | 45.2 | 42 | 0.1 | 12.7 | 16 | 0 | 1006 | -40.23 | Left Open full
GV19 |  | 0.6 | 2.5 | 19.1 | 77.8 | 2 | 0 | 1006 | 1.16 | Left Off
GV20 |  | 0.1 | 1.4 | 19.8 | 78.7 | 0 | 0 | 1006 | 0.04 | Left Off
GV 22 + CVs |  | 0.7 | 2.6 | 17.9 | 78.8 | 0 | 0 | 1006 | 0 | Left Off
GV23 |  | 0.2 | 1.7 | 19.5 | 78.6 | 0 | 0 | 1006 | 0 | Left Off
GV24 |  | 57.2 | 41.1 | 0.3 | 1.4 | 4 | 1 | 1006 | -23.92 | Left Open Full
GV25 |  | 39.1 | 36.5 | 0.2 | 24.2 | 6 | 10 | 1006 | -44.13 | Reg closed to cracked
GV26/A |  | 41.8 | 35.1 | 1.9 | 21.2 | 0 | 4 | 1006 | -44.67 | Reg closed to cracked
GV27+28 / B+C |  | 42.1 | 36.3 | 0.2 | 21.4 | 1 | 3 | 1006 | -28.68 | left open full
GV30 |  | 34 | 34 | 0.2 | 31.8 | 0 | 0 | 1006 | -38.27 | Left Open Full (needs new valve fixing tomorrow.)
GV31 |  | 48.6 | 38.2 | 0.9 | 12.3 | 0 | 0 | 1006 | -35.08 | Left Open full
GV32 |  | 52.9 | 40.3 | 1.1 | 5.7 | 0 | 0 | 1006 | -18.42 | reg opened half way
GV33 |  | 34.3 | 32.4 | 1.2 | 32.1 | 0 | 0 | 1006 | -30.92 | reg closed
GV34 |  | 41.1 | 22.6 | 1.3 | 35 | 0 | 0 | 1006 | -15.23 | reg cracked open
RP6.1 |  | 0.2 | 2.9 | 20 | 76.9 | 0 | 0 | 1006 | 0.03 | Left Off
LC1B |  | 32.8 | 20.4 | 7.8 | 39 | 6 | 0 | 1006 | 0.1 | left Off
LC1.1 |  | 52.4 | 19.6 | 0.3 | 27.7 | 0 | 0 | 1006 | -33.28 | Left Open Full
LC2R? |  | 44.9 | 35.6 | 0.2 | 19.3 | 0 | 0 | 1006 | -44 | Reg opened 3/4
GV 2.1 |  | 44.7 | 33.3 | 4 | 18 | 9 | 0 | 1006 | -41.68 | Reg closed to cracked
GV 2.2+ LC2B |  | 32.5 | 20.4 | 8.3 | 38.8 | 11 | 7 | 1006 | -8.14 | reg closed
GV / LC3.1 + LC3 |  | 51 | 32.3 | 3 | 13.7 | 5 | 0 | 1006 | 1.01 | Reg cracked open
LC4B |  | 35 | 29.5 | 2.3 | 33.2 | 10 | 0 | 1006 | -36.21 | Reg closed too cracked
LC5 |  | 58.9 | 40.5 | 0.3 | 0.3 | 0 | 0 | 1006 | -5.21 | Reg cracked open
LC6 |  | 39.5 | 29.6 | 5.8 | 25.1 | 0 | 0 | 1006 | -8.26 | Reg closed high o2
GV29D + LC6B |  | 50.1 | 39.8 | 0.4 | 9.7 | 1 | 3 | 1006 | -36.49 | Left Open Full
PW1 |  | 39.6 | 19.9 | 2.1 | 38.4 | 0 | 0 | 1006 | 0.21 | Left Off bad gas high o2
PW2 |  | 44.2 | 18.5 | 1.1 | 36.2 | 0 | 0 | 1006 | -9.98 | left Cracked Open
PW3 |  | 18.4 | 15.6 | 3.2 | 62.8 | 0 | 0 | 1006 | 0.36 | left off bad gas
PW4 |  | 30.6 | 18 | 3.3 | 48.1 | 0 | 0 | 1006 | 0.21 | left off
PW5 |  | 37.9 | 14.9 | 4 | 43.2 | 0 | 0 | 1006 | 0.89 | left off
PW6 |  | 45.2 | 30.3 | 0.4 | 24.1 | 0 | 0 | 1006 | -19.55 | Left Opened Full
Point: Cap Vent |  | Not connected. N/A
Flare | 14:20 | 46 | 36.6 | 0.7 | 16.7 | 4 | 0 | 1006 | 166 | Gas improved slightly. Engine 510

## October
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-10-02
Weather: | dry
Wind conditions: | calm
Air Temperature: | 14 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0.1 | 0.9 | 20 | 79 | 0 | 0 | 1003 | -0.35 | 1 | 8.8
BK BH 3 | 10:24 | 0.4 | 1.3 | 19.2 | 79.1 | 0 | 0 | 1003 | 0.76 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 0.8 | 20.3 | 78.9 | 0 | 0 | 1003 | 0.41 | 1 | 5.1
BK BH 5 | 10:28 | 0 | 0.4 | 20 | 79.6 | 0 | 0 | 1003 | 0.56 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1003 | 0.52 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 1.3 | 20.3 | 78.4 | 0 | 0 | 1003 | 0.48 | 1 | 10
BK BH 8 | 10:38 | 28.9 | 1.1 | 19.7 | 50.3 | 0 | 0 | 1003 | -0.15 | 32.2 | 3.6
BK BH 9 | 10:44 | 28.1 | 1.5 | 20 | 50.4 | 0 | 0 | 1003 | 0.36 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 1003 | -0.25 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 1003 | 0.16 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1003 | 0.87 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 1003 | -0.11 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1003 | 0.35 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1003 | -0.56 | 1 | 17.6
BK BH 16 | 11:18 | 0.2 | 0.8 | 20 | 79 | 0 | 0 | 1003 | 0.48 | 1 | 11.4
BK BH 17 | 11:25 | 0.7 | 1.1 | 19.6 | 78.6 | 0 | 0 | 1003 | -0.11 | 1 | 12.9
BK BH 18 | 9:51 | 0.2 | 2.3 | 19.8 | 77.7 | 0 | 0 | 1003 | 0.25 | 6.8 | 21.2
BK BH 19 | 9:55 | 0.4 | 1.9 | 19.4 | 78.3 | 0 | 0 | 1003 | 0.69 | 1 | 11.2
BK BH 20 | 9:58 | 0.6 | 5.4 | 20.2 | 73.8 | 0 | 0 | 1003 | -0.17 | 1 | 10.7
BK BH 21 | 10:03 | 0.5 | 6.8 | 19.6 | 73.1 | 0 | 0 | 1003 | 0.02 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 1003 | 0.39 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 0.6 | 18.9 | 80.5 | 0 | 0 | 1003 | -0.42 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1003 | 0.28 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-10-09
Weather: | dry
Wind conditions: | calm
Air Temperature: | 12 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0.2 | 2 | 20.2 | 77.6 | 0 | 0 | 997 | -0.54 | 1 | 8.8
BK BH 3 | 10:08 | 0.6 | 1.7 | 19.6 | 78.1 | 0 | 0 | 997 | 0.38 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 997 | 0.42 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 0.5 | 19.8 | 79.7 | 0 | 0 | 997 | -0.01 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 997 | 0.21 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 1 | 20 | 79 | 0 | 0 | 997 | 0.36 | 1 | 10
BK BH 8 | 10:22 | 30 | 1.2 | 19.5 | 49.3 | 0 | 0 | 997 | 0.58 | 32.2 | 3.6
BK BH 9 | 10:28 | 28.7 | 1.4 | 19.1 | 50.8 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 0.5 | 19.7 | 79.8 | 0 | 0 | 997 | 0.68 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 997 | 0.87 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 997 | 0.59 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 997 | 0.23 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 997 | 0.87 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 997 | -0.15 | 1 | 17.6
BK BH 16 | 11:02 | 0.3 | 0.7 | 19.2 | 79.8 | 0 | 0 | 997 | 0.23 | 1 | 11.4
BK BH 17 | 11:09 | 0.5 | 1.2 | 19.9 | 78.4 | 0 | 0 | 997 | -0.46 | 1 | 12.9
BK BH 18 | 9:35 | 0.4 | 2.3 | 20.2 | 77.1 | 0 | 0 | 997 | 0.68 | 6.8 | 21.2
BK BH 19 | 9:39 | 0.2 | 1.8 | 18.9 | 79.1 | 0 | 0 | 997 | 0.78 | 1 | 11.2
BK BH 20 | 9:42 | 0.3 | 5 | 19.6 | 75.1 | 0 | 0 | 997 | -0.15 | 1 | 10.7
BK BH 21 | 9:47 | 0.2 | 6 | 19.8 | 74 | 0 | 0 | 997 | 0.24 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 997 | 0.25 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 997 | -0.78 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 997 | 0.52 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-10-16
Weather: | slight rain
Wind conditions: | Breezy
Air Temperature: | 13 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0.4 | 2.3 | 20 | 77.3 | 0 | 0 | 1001 | -0.96 | 1 | 8.8
BK BH 3 | 9:51 | 0.5 | 1.5 | 19.8 | 78.2 | 0 | 0 | 1001 | 0.36 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1001 | -0.24 | 1 | 5.1
BK BH 5 | 9:55 | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 1001 | 0.49 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1001 | 0.87 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1001 | 0.53 | 1 | 10
BK BH 8 | 10:05 | 29.8 | 1 | 19.1 | 50.1 | 0 | 0 | 1001 | 0.26 | 32.2 | 3.6
BK BH 9 | 10:11 | 28.1 | 1.2 | 19.4 | 51.3 | 0 | 0 | 1001 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1001 | 0.75 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1001 | 0.21 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 0.5 | 20.1 | 79.4 | 0 | 0 | 1001 | -0.44 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 1001 | 0.63 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 1001 | 0.24 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1001 | -0.16 | 1 | 17.6
BK BH 16 | 10:45 | 0.4 | 0.9 | 19.4 | 79.3 | 0 | 0 | 1001 | 0.94 | 1 | 11.4
BK BH 17 | 10:52 | 0.6 | 1.4 | 20.2 | 77.8 | 0 | 0 | 1001 | 0.87 | 1 | 12.9
BK BH 18 | 9:18 | 0.4 | 2 | 19.2 | 78.4 | 0 | 0 | 1001 | -0.12 | 6.8 | 21.2
BK BH 19 | 9:22 | 0.1 | 1.6 | 19.4 | 78.9 | 0 | 0 | 1001 | 0.35 | 1 | 11.2
BK BH 20 | 9:25 | 0.5 | 5.8 | 20 | 73.7 | 0 | 0 | 1001 | -0.78 | 1 | 10.7
BK BH 21 | 9:30 | 0.3 | 5.2 | 19.2 | 75.3 | 0 | 0 | 1001 | 0.63 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 1001 | 0.25 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 1001 | -0.14 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1001 | 0.71 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-10-23
Weather: | slight rain
Wind conditions: | Breezy
Air Temperature: | 15 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0.2 | 2 | 19.9 | 77.9 | 0 | 0 | 1002 | -0.52 | 1 | 8.8
BK BH 3 | 10:28 | 0.4 | 1.4 | 19.6 | 78.6 | 0 | 0 | 1002 | -0.12 | 1 | 3.1
BK BH 4 | 10:30 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1002 | 0.41 | 1 | 5.1
BK BH 5 | 10:33 | 0 | 0.3 | 19.8 | 79.9 | 0 | 0 | 1002 | 0.52 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1002 | 0.77 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 1002 | 0.52 | 1 | 10
BK BH 8 | 10:42 | 30.1 | 1.2 | 19.2 | 49.5 | 0 | 0 | 1002 | 0.46 | 32.2 | 3.6
BK BH 9 | 10:48 | 28.9 | 1 | 19.9 | 50.2 | 0 | 0 | 1002 | -0.14 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 0.4 | 20.3 | 79.3 | 0 | 0 | 1002 | 0.36 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 1002 | -0.25 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 1002 | -0.11 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 1002 | 0.69 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 1002 | 0.75 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1002 | -0.11 | 1 | 17.6
BK BH 16 | 11:22 | 0.3 | 0.8 | 19.5 | 79.4 | 0 | 0 | 1002 | 0.29 | 1 | 11.4
BK BH 17 | 11:29 | 0.4 | 1.1 | 20.8 | 77.7 | 0 | 0 | 1002 | -0.26 | 1 | 12.9
BK BH 18 | 9:55 | 0.4 | 2.3 | 19.5 | 77.8 | 0 | 0 | 1002 | 0.52 | 6.8 | 21.2
BK BH 19 | 9:59 | 0.2 | 1.7 | 20.3 | 77.8 | 0 | 0 | 1002 | 0.46 | 1 | 11.2
BK BH 20 | 10:02 | 0.6 | 5 | 20.1 | 74.3 | 0 | 0 | 1002 | -0.68 | 1 | 10.7
BK BH 21 | 10:07 | 0.1 | 5.4 | 19.5 | 75 | 0 | 0 | 1002 | -0.08 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1002 | 0.21 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | -0.42 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1002 | 0.38 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-10-30
Weather: | calm dry
Wind conditions: | Breezy
Air Temperature: | 14 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:48 | 0.3 | 2.3 | 19.9 | 77.5 | 0 | 0 | 1000 | -0.25 | 1 | 8.8
BK BH 3 | 10:53 | 0.2 | 1.1 | 19.6 | 79.1 | 0 | 0 | 1000 | 0.41 | 1 | 3.1
BK BH 4 | 10:54 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1000 | -0.21 | 1 | 5.1
BK BH 5 | 10:56 | 0 | 0.2 | 19.8 | 80 | 0 | 0 | 1000 | 0.12 | 1 | 1.5
BK BH 6 | 11:00 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1000 | 0.26 | 1 | 1.5
BK BH 7 | 11:04 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1000 | 0.45 | 1 | 10
BK BH 8 | 11:07 | 29.6 | 1 | 19.2 | 50.2 | 0 | 0 | 1000 | -0.12 | 32.2 | 3.6
BK BH 9 | 11:13 | 27.4 | 1.2 | 19.9 | 51.5 | 0 | 0 | 1000 | 0.36 | 29.6 | 10.4
BK BH 10 | 11:18 | 0 | 0.3 | 20.3 | 79.4 | 0 | 0 | 1000 | -0.15 | 1 | 3.9
BK BH 11 | 11:30 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1000 | 0.73 | 1 | 6.5
BK BH 12 | 11:34 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 1000 | -0.42 | 1 | 6.6
BK BH 13 | 11:38 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 1000 | 0.36 | 1 | 9.4
BK BH 14 | 11:41 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1000 | -0.11 | 1 | 3.5
BK BH 15 | 11:44 | 0 | 1.6 | 20.3 | 78.1 | 0 | 0 | 1000 | 0.74 | 1 | 17.6
BK BH 16 | 11:47 | 0.2 | 1.1 | 19.5 | 79.2 | 0 | 0 | 1000 | 0.23 | 1 | 11.4
BK BH 17 | 11:54 | 0.6 | 1.4 | 20.8 | 77.2 | 0 | 0 | 1000 | -0.18 | 1 | 12.9
BK BH 18 | 10:20 | 1 | 2 | 19.5 | 77.5 | 0 | 0 | 1000 | 0.92 | 6.8 | 21.2
BK BH 19 | 10:24 | 0.3 | 1.9 | 20.3 | 77.5 | 0 | 0 | 1000 | 0.37 | 1 | 11.2
BK BH 20 | 10:27 | 0.5 | 5.3 | 20.1 | 74.1 | 0 | 0 | 1000 | -0.18 | 1 | 10.7
BK BH 21 | 10:32 | 0.3 | 5 | 19.5 | 75.2 | 0 | 0 | 1000 | 0.29 | 1 | 21.7
BK BH 23 | 10:37 | 0 | 0.4 | 19.6 | 80 | 0 | 0 | 1000 | -0.11 | 1 | 7.3
BK BH 24 | 10:40 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 1000 | 0.54 | 1 | 1.5
BK BH 25 | 10:44 | 0 | 1.4 | 20.3 | 78.3 | 0 | 0 | 1000 | 0.87 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-10-08
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 16 | oC
Instrument: |  | GA2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2015-02-18
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 9:30 | 44.2 | 33.2 | 0.9 | 21.7 | 6 | 0 | 999 | 155
GV1 |  | 0.4 | 1.6 | 10.2 | 87.8 | 0 | 4 | 999 | 0.01 | left Off
GV2 |  | 52.3 | 19.6 | 1 | 27.1 | 9 | 8 | 999 | -41.28 | Reg cracked open good gas
GV3 |  | 58.1 | 33.2 | 0.6 | 8.1 | 4 | 5 | 999 | -35.28 | Left Open full
GV4 |  | 39.6 | 27.1 | 1.1 | 32.2 | 4 | 0 | 999 | 0.01 | reg closed bad gas
GV5+R1 |  | 48.1 | 30.2 | 4.6 | 17.1 | 0 | 0 | 999 | 0.23 | Left Off high o2
GV6 |  | 50.2 | 30.9 | 0.6 | 18.3 | 2 | 0 | 999 | -40.28 | Left Open Full
GV7 |  | 29.1 | 25.1 | 3.2 | 42.6 | 0 | 0 | 999 | -0.25 | Reg Closed
GV8 |  | 32.6 | 25.7 | 4.1 | 37.6 | 8 | 0 | 999 | 0.12 | Left Off
GV9 |  | 55.7 | 33.6 | 0.2 | 10.5 | 9 | 0 | 999 | -41.89 | Left Open Full
GV9.1 |  | 0.3 | 0.5 | 19.6 | 79.6 | 0 | 0 | 999 | 0.02 | left off
GV10 |  | 50.1 | 32.2 | 0.8 | 16.9 | 4 | 0 | 999 | -8.54 | reg opened full
GV11 |  | 50.1 | 36.5 | 0.9 | 12.5 | 4 | 0 | 999 | -17.45 | reg opened half way good gas
GV12+R3 |  | 51.8 | 32.5 | 1.1 | 14.6 | 14 | 0 | 999 | -34.78 | Left Open Full
GV13 |  | 0.6 | 1.4 | 16.5 | 81.5 | 0 | 0 | 999 | 0 | Left Off
GV14 |  | 19.8 | 13 | 1.1 | 66.1 | 2 | 1 | 999 | -0.15 | Left turned off
GV15 |  | 55.2 | 39.4 | 0.4 | 5 | 14 | 2 | 999 | -41.27 | Left Open Full
GV16 |  | 12.6 | 8.2 | 15 | 64.2 | 12 | 0 | 999 | 0.12 | left off
GV17+LC4 |  | 38.4 | 25.4 | 6.3 | 29.9 | 2 | 0 | 999 | 0 | Left off
GV18+21 |  | 46.2 | 40.1 | 0.3 | 13.4 | 13 | 0 | 999 | -42.36 | Left Open full
GV19 |  | 0.8 | 2.4 | 19.6 | 77.2 | 3 | 0 | 999 | 1.16 | Left Off
GV20 |  | 0.2 | 1.6 | 20.1 | 78.1 | 0 | 1 | 999 | 0.21 | Left Off
GV 22 + CVs |  | 0.6 | 2.1 | 16.5 | 80.8 | 0 | 0 | 999 | 0 | Left Off
GV23 |  | 0.3 | 1.5 | 20.1 | 78.1 | 0 | 0 | 999 | 0 | Left Off
GV24 |  | 55.6 | 42.1 | 0.4 | 1.9 | 5 | 3 | 999 | -32.59 | Left Open Full
GV25 |  | 48.2 | 35.2 | 1.1 | 15.5 | 8 | 8 | 999 | -8.71 | left cracked open
GV26/A |  | 44.5 | 33.1 | 1 | 21.4 | 0 | 5 | 999 | -14.52 | Left crcked
GV27+28 / B+C |  | 50.1 | 33.1 | 0.3 | 16.5 | 2 | 2 | 999 | -32.99 | left open full
GV30 |  | 54.1 | 35.7 | 0.4 | 9.8 | 0 | 0 | 999 | -40 | Left Open Full
GV31 |  | 49.8 | 36.5 | 0.6 | 13.1 | 0 | 0 | 999 | -36.21 | Left Open full
GV32 |  | 50.1 | 38.7 | 1 | 10.2 | 0 | 0 | 999 | -19.02 | reg opened half way
GV33 |  | 31.8 | 30.2 | 1.5 | 36.5 | 0 | 1 | 999 | 0.23 | Left closed bad gas
GV34 |  | 48.7 | 20 | 1 | 30.3 | 0 | 0 | 999 | -12.58 | left cracked open
RP6.1 |  | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 999 | 0.03 | Left Off
LC1B |  | 33.8 | 19.8 | 7 | 39.4 | 6 | 0 | 999 | 0.1 | left Off
LC1.1 |  | 50.1 | 19.1 | 0.4 | 30.4 | 0 | 1 | 999 | -35.69 | Left Open Full
LC2R? |  | 47.1 | 33.5 | 1.2 | 18.2 | 0 | 0 | 999 | -9.21 | reg closed too cracked high o2
GV 2.1 |  | 45.8 | 32.1 | 1 | 21.1 | 10 | 0 | 999 | -8.47 | left cracked open
GV 2.2+ LC2B |  | 35.2 | 19.6 | 7.1 | 38.1 | 15 | 6 | 999 | 0.23 | reg closed
GV / LC3.1 + LC3 |  | 49.9 | 27.4 | 1.1 | 21.6 | 6 | 0 | 999 | -5.07 | left cracked open
LC4B |  | 45.6 | 31.5 | 0.9 | 22 | 14 | 0 | 999 | -8.93 | left cracked open
LC5 |  | 51.4 | 30.2 | 1.2 | 17.2 | 0 | 0 | 999 | -7.14 | left cracked open
LC6 |  | 38.2 | 27.4 | 4.1 | 30.3 | 0 | 0 | 999 | 0.33 | Left closed bad gas
GV29D + LC6B |  | 49.9 | 38.1 | 0.3 | 11.7 | 2 | 2 | 999 | -40.89 | Left Open Full
PW1 |  | 38.4 | 18.2 | 2.5 | 40.9 | 0 | 0 | 999 | 0.18 | Left Off bad gas high o2
PW2 |  | 48.1 | 18.1 | 1 | 32.8 | 0 | 0 | 999 | -10.28 | left Cracked Open
PW3 |  | 17.4 | 12.3 | 3.9 | 66.4 | 0 | 0 | 999 | 0.21 | left off bad gas
PW4 |  | 31.2 | 16.5 | 3.4 | 48.9 | 0 | 0 | 999 | 0.39 | left off
PW5 |  | 35.2 | 15 | 4.9 | 44.9 | 0 | 0 | 999 | 0.54 | left off
PW6 |  | 50.1 | 27.4 | 0.3 | 22.2 | 0 | 0 | 999 | -32.58 | Left Opened Full
Point: Cap Vent; mb: 999 |  | Not connected. N/A
Flare | 14:00 | 48.7 | 36.9 | 0.5 | 13.9 | 2 | 0 | 999 | 166 | Gas improved slightly. Engine 510

## November
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-11-06
Weather: | calm dry
Wind conditions: | Calm
Air Temperature: | 14 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:52 | 0.1 | 2 | 20.1 | 77.8 | 0 | 0 | 1002 | 0.72 | 1 | 8.8
BK BH 3 | 9:57 | 0.1 | 1 | 20.3 | 78.6 | 0 | 0 | 1002 | -0.48 | 1 | 3.1
BK BH 4 | 10:00 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1002 | 0.58 | 1 | 5.1
BK BH 5 | 10:02 | 0 | 0.3 | 19.5 | 80.2 | 0 | 0 | 1002 | 0.61 | 1 | 1.5
BK BH 6 | 10:04 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 1002 | 0.72 | 1 | 1.5
BK BH 7 | 10:08 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.84 | 1 | 10
BK BH 8 | 10:11 | 30.1 | 1.7 | 19.4 | 48.8 | 0 | 0 | 1002 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:16 | 28.1 | 1.5 | 19.3 | 51.1 | 0 | 0 | 1002 | 0.78 | 29.6 | 10.4
BK BH 10 | 10:22 | 0 | 0.2 | 20.1 | 79.7 | 0 | 0 | 1002 | 0.78 | 1 | 3.9
BK BH 11 | 10:34 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1002 | -0.62 | 1 | 6.5
BK BH 12 | 10:38 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 1002 | 0.47 | 1 | 6.6
BK BH 13 | 10:42 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1002 | -0.97 | 1 | 9.4
BK BH 14 | 10:45 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1002 | 0.41 | 1 | 3.5
BK BH 15 | 10:48 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | 0.56 | 1 | 17.6
BK BH 16 | 10:51 | 0.1 | 1.2 | 19.6 | 79.1 | 0 | 0 | 1002 | 1.27 | 1 | 11.4
BK BH 17 | 10:58 | 0.3 | 1.5 | 20.5 | 77.7 | 0 | 0 | 1002 | 0.89 | 1 | 12.9
BK BH 18 | 9:24 | 0.1 | 2.3 | 19.7 | 77.9 | 0 | 0 | 1002 | 0.59 | 6.8 | 21.2
BK BH 19 | 9:28 | 0.2 | 1.5 | 20.1 | 78.2 | 0 | 0 | 1002 | 0.78 | 1 | 11.2
BK BH 20 | 9:31 | 0.2 | 5 | 20.3 | 74.5 | 0 | 0 | 1002 | 0.5 | 1 | 10.7
BK BH 21 | 9:26 | 0.1 | 4.8 | 19.6 | 75.5 | 0 | 0 | 1002 | 0.56 | 1 | 21.7
BK BH 23 | 9:41 | 0 | 0.3 | 19.8 | 79.9 | 0 | 0 | 1002 | 0.82 | 1 | 7.3
BK BH 24 | 9:44 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1002 | -0.89 | 1 | 1.5
BK BH 25 | 9:48 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-11-13
Weather: | Slight rain
Wind conditions: | breezy
Air Temperature: | 15 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:22 | 0.2 | 2.5 | 19.9 | 77.4 | 0 | 0 | 997 | 0.61 | 1 | 8.8
BK BH 3 | 10:27 | 0.1 | 1.2 | 19.7 | 79 | 0 | 0 | 997 | -0.51 | 1 | 3.1
BK BH 4 | 10:29 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 997 | 0.41 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.6 | 20.2 | 79.2 | 0 | 0 | 997 | -0.12 | 1 | 1.5
BK BH 6 | 10:34 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 997 | 0.62 | 1 | 1.5
BK BH 7 | 10:38 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 997 | 0.62 | 1 | 10
BK BH 8 | 10:41 | 29.9 | 1.5 | 19.6 | 49 | 0 | 0 | 997 | 0.55 | 32.2 | 3.6
BK BH 9 | 10:46 | 28.4 | 1.2 | 20.1 | 50.3 | 0 | 0 | 997 | 0.63 | 29.6 | 10.4
BK BH 10 | 10:52 | 0 | 0.5 | 19.8 | 79.7 | 0 | 0 | 997 | 0.8 | 1 | 3.9
BK BH 11 | 11:04 | 0 | 1.6 | 20.3 | 78.1 | 0 | 0 | 997 | -0.49 | 1 | 6.5
BK BH 12 | 11:08 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | 0.3 | 1 | 6.6
BK BH 13 | 11:12 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 997 | -0.71 | 1 | 9.4
BK BH 14 | 11:15 | 0 | 1.7 | 19.9 | 78.4 | 0 | 0 | 997 | 0.4 | 1 | 3.5
BK BH 15 | 11:18 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | 0.44 | 1 | 17.6
BK BH 16 | 11:21 | 0.2 | 1.4 | 19.9 | 78.5 | 0 | 0 | 997 | 0.81 | 1 | 11.4
BK BH 17 | 11:28 | 0.5 | 1.4 | 20.2 | 77.9 | 0 | 0 | 997 | 0.5 | 1 | 12.9
BK BH 18 | 9:54 | 0.3 | 2.5 | 19.9 | 77.3 | 0 | 0 | 997 | -0.53 | 6.8 | 21.2
BK BH 19 | 9:58 | 0.1 | 1.4 | 20 | 78.5 | 0 | 0 | 997 | 0.5 | 1 | 11.2
BK BH 20 | 10:01 | 0.1 | 5.2 | 20.1 | 74.6 | 0 | 0 | 997 | 0.59 | 1 | 10.7
BK BH 21 | 10:06 | 0.3 | 5.9 | 19.8 | 74 | 0 | 0 | 997 | 0.44 | 1 | 21.7
BK BH 23 | 10:11 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 997 | 0.78 | 1 | 7.3
BK BH 24 | 10:14 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 997 | -0.78 | 1 | 1.5
BK BH 25 | 10:18 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 997 | 0.41 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-11-20
Weather: | dry
Wind conditions: | breezy
Air Temperature: | 13 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:38 | 0.1 | 2.1 | 19.7 | 78.1 | 0 | 0 | 998 | -0.52 | 1 | 8.8
BK BH 3 | 11:43 | 0.2 | 1.3 | 20 | 78.5 | 0 | 0 | 998 | 0.52 | 1 | 3.1
BK BH 4 | 11:45 | 0 | 1.1 | 20.2 | 78.7 | 0 | 0 | 998 | 0.45 | 1 | 5.1
BK BH 5 | 11:48 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 998 | 0.32 | 1 | 1.5
BK BH 6 | 11:50 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 998 | 0.32 | 1 | 1.5
BK BH 7 | 11:54 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 998 | 0.42 | 1 | 10
BK BH 8 | 11:57 | 29.1 | 1.1 | 19.8 | 50 | 0 | 0 | 998 | 0.63 | 32.2 | 3.6
BK BH 9 | 12:03 | 28.9 | 1.4 | 20 | 49.7 | 0 | 0 | 998 | 0.25 | 29.6 | 10.4
BK BH 10 | 12:08 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | -0.14 | 1 | 3.9
BK BH 11 | 12:20 | 0 | 1.9 | 19.4 | 78.7 | 0 | 0 | 998 | 0.75 | 1 | 6.5
BK BH 12 | 12:24 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 998 | -0.63 | 1 | 6.6
BK BH 13 | 12:28 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 998 | -0.25 | 1 | 9.4
BK BH 14 | 12:31 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 998 | 0.24 | 1 | 3.5
BK BH 15 | 12:34 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 998 | 0.69 | 1 | 17.6
BK BH 16 | 12:37 | 0.1 | 1 | 20.1 | 78.8 | 0 | 0 | 998 | -0.15 | 1 | 11.4
BK BH 17 | 12:44 | 0.4 | 1.2 | 20.1 | 78.3 | 0 | 0 | 998 | -0.42 | 1 | 12.9
BK BH 18 | 11:10 | 0.2 | 2.1 | 19.6 | 78.1 | 0 | 0 | 998 | -0.11 | 6.8 | 21.2
BK BH 19 | 11:14 | 0.1 | 1.6 | 20.1 | 78.2 | 0 | 0 | 998 | 0.89 | 1 | 11.2
BK BH 20 | 11:17 | 0.2 | 5 | 19.6 | 75.2 | 0 | 0 | 998 | -0.72 | 1 | 10.7
BK BH 21 | 11:22 | 0.2 | 5.5 | 19.5 | 74.8 | 0 | 0 | 998 | 0.58 | 1 | 21.7
BK BH 23 | 11:27 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 998 | 0.71 | 1 | 7.3
BK BH 24 | 11:30 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 998 | 0.74 | 1 | 1.5
BK BH 25 | 11:34 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 998 | -0.17 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2014-11-27
Weather: | dry
Wind conditions: | breezy
Air Temperature: | 11 | OC
Instrument: | GA2000
Serial No: | GA10692
Calibrated To: | 2015-02-18
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:52 | 0.2 | 2.4 | 19.9 | 77.5 | 0 | 0 | 1002 | -0.49 | 1 | 8.8
BK BH 3 | 11:57 | 0.1 | 1.9 | 20.2 | 77.8 | 0 | 0 | 1002 | 0.85 | 1 | 3.1
BK BH 4 | 11:59 | 0 | 0.9 | 20.2 | 78.9 | 0 | 0 | 1002 | 0.75 | 1 | 5.1
BK BH 5 | 12:01 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1002 | 0.48 | 1 | 1.5
BK BH 6 | 12:04 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.12 | 1 | 1.5
BK BH 7 | 12:08 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1002 | -0.11 | 1 | 10
BK BH 8 | 12:11 | 28.5 | 1.4 | 20.1 | 50 | 0 | 0 | 1002 | 0.56 | 32.2 | 3.6
BK BH 9 | 12:17 | 28.7 | 1.5 | 20.1 | 49.7 | 0 | 0 | 1002 | 0.47 | 29.6 | 10.4
BK BH 10 | 12:22 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1002 | -0.18 | 1 | 3.9
BK BH 11 | 12:34 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1002 | 0.24 | 1 | 6.5
BK BH 12 | 12:38 | 0 | 1.4 | 20.4 | 78.2 | 0 | 0 | 1002 | 0.15 | 1 | 6.6
BK BH 13 | 12:42 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | 0.75 | 1 | 9.4
BK BH 14 | 12:45 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | -0.11 | 1 | 3.5
BK BH 15 | 12:48 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 1002 | 0.63 | 1 | 17.6
BK BH 16 | 12:51 | 0.2 | 1.2 | 20.3 | 78.3 | 0 | 0 | 1002 | 0.87 | 1 | 11.4
BK BH 17 | 12:58 | 0.3 | 1.5 | 19.8 | 78.4 | 0 | 0 | 1002 | 0.98 | 1 | 12.9
BK BH 18 | 11:24 | 0.1 | 2 | 19.8 | 78.1 | 0 | 0 | 1002 | -0.14 | 6.8 | 21.2
BK BH 19 | 11:28 | 0.2 | 1.4 | 20.3 | 78.1 | 0 | 0 | 1002 | 0.26 | 1 | 11.2
BK BH 20 | 11:31 | 0.1 | 5.2 | 19.5 | 75.2 | 0 | 0 | 1002 | 0.57 | 1 | 10.7
BK BH 21 | 11:36 | 0.2 | 5.9 | 19.8 | 74.1 | 0 | 0 | 1002 | -0.11 | 1 | 21.7
BK BH 23 | 11:41 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1002 | 0.32 | 1 | 7.3
BK BH 24 | 11:44 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | -0.63 | 1 | 1.5
BK BH 25 | 11:48 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1002 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2014-11-05
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 14 | oC
Instrument: |  | GA2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2015-02-18
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb
Flare | 9:10 | 45.2 | 31.5 | 0.6 | 22.7 | 3 | 0 | 1002 | 92
GV1 |  | 0.2 | 1.5 | 9.9 | 88.4 | 2 | 5 | 1002 | 0.01 | left Off
GV2 |  | 51.1 | 18.9 | 1.1 | 28.9 | 11 | 6 | 1002 | -19.25 | Left cracked open
GV3 |  | 56.9 | 29.8 | 0.5 | 12.8 | 3 | 2 | 1002 | -32.14 | Left Open full
GV4 |  | 41.2 | 23.9 | 1.4 | 33.5 | 2 | 0 | 1002 | 0.01 | Left off high o2
GV5+R1 |  | 45.8 | 29.6 | 3.6 | 21 | 0 | 0 | 1002 | 0.17 | Left Off high o2
GV6 |  | 50.9 | 31.2 | 0.7 | 17.2 | 1 | 0 | 1002 | -35.47 | Left Open Full
GV7 |  | 28.6 | 24.1 | 3 | 44.3 | 0 | 0 | 1002 | 0.17 | Left closed bad gas
GV8 |  | 34.8 | 22.7 | 3.5 | 39 | 7 | 0 | 1002 | 0.08 | Left Off
GV9 |  | 52.3 | 30.1 | 0.5 | 17.1 | 10 | 0 | 1002 | -39.68 | Left Open Full
GV9.1 |  | 0.1 | 0.7 | 19.2 | 80 | 0 | 0 | 1002 | 0.05 | left off
GV10 |  | 44.5 | 33.5 | 1 | 21 | 3 | 0 | 1002 | -9.38 | Left cracked open
GV11 |  | 48.6 | 30.2 | 1.1 | 20.1 | 2 | 0 | 1002 | -14.87 | Reg closed too cracked high o2
GV12+R3 |  | 50.2 | 30.9 | 0.5 | 18.4 | 10 | 0 | 1002 | -35.23 | Left Open Full
GV13 |  | 0.9 | 0.9 | 15.2 | 83 | 0 | 0 | 1002 | 0.12 | Left Off
GV14 |  | 41.5 | 10.2 | 1.3 | 47 | 3 | 3 | 1002 | 0.27 | Left off
GV15 |  | 52.8 | 32.4 | 0.5 | 14.3 | 17 | 1 | 1002 | -36.71 | Left Open Full
GV16 |  | 14.2 | 6.6 | 13.2 | 66 | 9 | 0 | 1002 | 0.17 | left off
GV17+LC4 |  | 40.2 | 22.3 | 6.9 | 30.6 | 2 | 0 | 1002 | 0.14 | Left off
GV18 |  | 45.2 | 39.9 | 0.2 | 14.7 | 11 | 0 | 1002 | -39.38 | Left Open full
GV19 |  | 0.5 | 2.1 | 19.9 | 77.5 | 3 | 0 | 1002 | 0.01 | Left Off
GV20 |  | 0.3 | 1.4 | 20.4 | 77.9 | 0 | 2 | 1002 | 0.21 | Left Off
GV 22 |  | 0.5 | 2 | 18.7 | 78.8 | 0 | 0 | 1002 | 0 | Left Off
GV23 |  | 0.2 | 1 | 19.9 | 78.9 | 0 | 0 | 1002 | 0 | Left Off
GV24 |  | 56.3 | 39.9 | 0.5 | 3.3 | 5 | 3 | 1002 | -27.84 | Left Open Full
GV25 |  | 46.2 | 32.5 | 1.2 | 20.1 | 6 | 5 | 1002 | -9.38 | left cracked open
GV26 + 27 |  | 50.1 | 31.4 | 0.5 | 18 | 2 | 1 | 1002 | -35.41 | Left Open Full
GV 28+ 29 |  | 55.9 | 29.9 | 0.2 | 14 | 4 | 3 | 1002 | -32.89 | Left Open Full
GVA |  | 48.6 | 30.5 | 1 | 19.9 | 6 | 5 | 1002 | -24.17 | Left Open Half way
GV B + C |  | 51.2 | 29.5 | 0.5 | 18.8 | 5 | 2 | 1002 | -30.07 | Left Open Full
GV30 |  | 52.3 | 33.5 | 0.5 | 13.7 | 0 | 0 | 1002 | -35.99 | Left Open Full
GV31 |  | 50.2 | 30.1 | 0.4 | 19.3 | 0 | 0 | 1002 | -32.52 | Left Open full
GV32 |  | 48.5 | 35.6 | 1 | 14.9 | 0 | 0 | 1002 | -17.48 | Left Opened half way
GV33 |  | 35.8 | 29.6 | 1.6 | 33 | 0 | 1 | 1002 | 0.14 | Left closed bad gas
GV34 |  | 46.9 | 19.9 | 1 | 32.2 | 0 | 0 | 1002 | -14.52 | left cracked open
RP6.1 |  | Not in use
LC1B |  | 35.6 | 19.6 | 6.5 | 38.3 | 5 | 0 | 1002 | 0.12 | left Off
LC1.1 |  | 42.3 | 17 | 2.1 | 38.6 | 0 | 1 | 1002 | 0.04 | Reg turned off high o2
LC2R? |  | 49.8 | 31.5 | 0.6 | 18.1 | 0 | 0 | 1002 | -26.7 | reg opened full
GV 2.1 |  | 48.9 | 35.2 | 1.1 | 14.8 | 8 | 0 | 1002 | -9.93 | left cracked open
GV 2.2+ LC2B |  | 32.6 | 20.1 | 6.5 | 40.8 | 12 | 6 | 1002 | 0.35 | Left off
GV / LC3.1 + LC3 |  | 46.8 | 25.4 | 1.2 | 26.6 | 7 | 0 | 1002 | -11.48 | Reg closed too cracked high o2
LC4B |  | 47.8 | 32.1 | 1 | 19.1 | 12 | 0 | 1002 | -10.24 | left cracked open
R4B |  | 26.8 | 20.1 | 3.6 | 49.5 | 6 | 0 | 1002 | 0.07 | Left OFF
LC5 |  | 50.1 | 31.5 | 1.3 | 17.1 | 0 | 0 | 1002 | -7.14 | Reg closed too cracked high o2
LC6 |  | 51.2 | 25.3 | 1.1 | 22.4 | 0 | 0 | 1002 | 0.33 | Reg cracked open good gas
LC6B |  | 50.2 | 27.8 | 1.2 | 20.8 | 3 | 2 | 1002 | 0.12 | Reg closed high o2
PW1 |  | 41.2 | 17.5 | 2 | 39.3 | 0 | 0 | 1002 | 0.05 | Left Off bad gas high o2
PW2 |  | 40.2 | 17.8 | 2 | 40 | 0 | 0 | 1002 | 0.23 | Reg closed
PW3 |  | 17.4 | 12.8 | 4.2 | 65.6 | 0 | 0 | 1002 | 0.14 | left off bad gas
PW4 |  | 32.5 | 18.9 | 4 | 44.6 | 0 | 0 | 1002 | 0.21 | left off
PW5 |  | 50.1 | 14.8 | 0.9 | 34.2 | 0 | 0 | 1002 | -8.97 | Reg cracked open good gas
PW6 |  | 52.1 | 26.8 | 0.3 | 20.8 | 0 | 0 | 1002 | -27.14 | Reg opened full
Point: Cap Vent |  | Not connected. N/A
Flare | 14:20 | 49 | 37.9 | 0.6 | 12.5 | 1 | 0 | 1002 | 98 | Gas improved slightly. Engine 500