## Slide 1
A well renowned collaborative team of expert water scientists and engineers
Pragmatic.Expert.Solutions
A well renowned collaborative team of expert water scientists and engineers
Water Resources Assessment

## Slide 2
Pragmatic.Expert.Solutions
@envireauwater
Structure
Presentation to Natural Resources Wales (NRW) to provide information on water resources and functioning of River Teme based on evidence collated by Envireau Water in discussion with Nick Rukin (rUKhydro) to incorporate his work on impact of discharge, ongoing monitoring and conceptual understanding.
Background
Environmental Setting
LowFlows2 Analysis
Flow Gauging Analysis
Local Impacts
Groundwater Flow Analysis
Resource Impact Analysis
Summary
Conceptual Model
Conclusions

## Slide 3: Background
Pragmatic.Expert.Solutions
@envireauwater
The Watkins Family have farmed the land since 1903 and always been aware that the river dries up during summer periods
Radnor Hills employs 200 people directly with a further 200 people employed locally in the supply chain.
Radnor Hills is the largest employer locally in Mid Wales.

## Slide 4: Background
Pragmatic.Expert.Solutions
@envireauwater
Radnor Hills Mineral Water Company have a total of 15 boreholes abstracting water from the bedrock and superficial deposits.
In 2019 applications were made to NRW and the Environment Agency to licence the abstraction under the Transitional Provisions Regulations. The following volumes were applied for and validated:
Raglan Mudstone Formation (Wales):
6 Boreholes, annual abstraction of 80,379 m3/yr
Welsh Superficial (Gravels);
6 Boreholes, annual abstraction of 155,212 m3/yr
English Superficial (Gravels):
3 Boreholes, annual abstraction of 60,833 m3/yr
Total annual abstraction 296,424 m3/yr
Radnor Hills have a permit (EPR:/AB3697CN) to discharge 194.4 m3/day to the gravels. This totals 70,956 m3/yr and is 24% of the total abstraction.

## Slide 5: Background
Pragmatic.Expert.Solutions
@envireauwater
The River Teme is a SSSI
The River Clun which is a SAC joins the River Teme SSSI at Leintwardine, ~6km downstream from Radnor Hills
The River Teme is a naturally ephemeral river and reaches of it dry up each year
Fish rescues were first witnessed 15 to 20 years ago, and have happened since
The NRW are determining the Transitional Provisions abstraction licence applications

## Slide 6: Environmental Setting
Pragmatic.Expert.Solutions
@envireauwater
River Clun SAC is upgradient of River Teme

## Slide 7: River Teme Losses & Gains Since 1996
Pragmatic.Expert.Solutions
@envireauwater
Ref. rUKhydro after ESI 2007 Fig 5.9
Very low flows pre-date Radnor Hills

## Slide 8: Geological Setting
Pragmatic.Expert.Solutions
@envireauwater
Discharge Point
(70,956 m3/yr)
Abstraction from groundwater
(296,424 m3/yr)

## Slide 9: River Teme Discharge Amounts (LowFlows2 Estimation)
Pragmatic.Expert.Solutions
@envireauwater
Calculated using LowFlows2 based on FEH Catchment Descriptors
Shows that Lingen Bridge and Buckton Bridge can be considered as one
LowFlows2 gives a quantitative assessment of the total volume of water in the valley based on runoff from the catchment
Location | LowFlows2 Results |  | 
 | Annual River Teme Discharge (m3/yr) | River Teme Discharge per km2 of catchment (m3/yr) | August River Teme Discharge (m3/month)
Knighton | 78,650,784 | 602,319 | 2,402,525
Lingen Bridge | 94,008,816 | 577,272 | 2,292,710
Buckton Bridge | 95,522,544 | 573,158 | 2,319,494
Notes: Lingen Bridge used as closest to Radnor. Buckton Bridge used in conceptual model and summary

## Slide 10: Flow Gauging
Pragmatic.Expert.Solutions
@envireauwater
Spot Flow Gauging has undertaken by the Environment Agency at Knighton Bridge, Milebrook, Lingen Bridge and Buckton Bridge over the years 1996 – 2021.
These measurements represent the flow in the river at the time of measurement only – they have been used as a guide here.
The gauging is not analogous to the LowFlows2 calculation. The gauging is the true flow in the river.
Gauging downstream also includes Knighton STW discharge at 910m3/day.
LowFlows2 provides an estimate of the water flowing down the valley based on HR Wallingford stochastic rainfall, and FEH catchment descriptors.
The catchment runoff partitions between the valley fill gravels and the river channel. The spot gauging quantifies the river channel flow.
The flow in the gravels must be estimated using hydrogeological methods.

## Slide 11: Comparison of Spot Flow Measurement per km2 catchment area
Pragmatic.Expert.Solutions
@envireauwater
Spot flow data from Environment Agency

## Slide 12: River Teme Valley Discharge
Pragmatic.Expert.Solutions
@envireauwater
Spot flow measurements at Lingen Bridge for July, August and September (selected as they had the most data points) were used to calculate an average monthly discharge, to compare with equivalent monthly discharge calculated using LowFlows2
Month | Spot Flow Average (m3/s) | LowFlows2 Average (m3/s)
July | 0.12 | 0.92
August | 0.09 | 0.86
September | 0.13 | 1.03
Month | Spot Flow Discharge (m3/month) | LowFlows2 Discharge (m3/month) | Difference (m3/month)
July | 320,069 | 2,453,414 | 2,133,346
August | 249,466 | 2,292,710 | 2,043,244
September | 335,589 | 2,674,944 | 2,339,355
Spot Flow Discharges are 11-15% of the discharge in the valley.
The difference represents the amount of water in the ground (bedrock and gravels), which accounts for 85-89% of the valley discharge during the summer months as a proportion of discharge at Leintwardine
Water in the
River
Water in the
Valley
Groundwater
(Bedrock and Gravel)
Notes: Lingen Bridge used as closest to Radnor. Buckton Bridge used in conceptual model and summary

## Slide 13: Local Impact
Pragmatic.Expert.Solutions
@envireauwater
Shallow Piezometers show that groundwater flow is down the valley and not into the river.
Perturbations likely due to changes in permeability (drain lines)
Groundwater Flow Direction

## Slide 14: Local Impact
Pragmatic.Expert.Solutions
@envireauwater
No evidence of abstraction modifying the contours.
No evidence of abstraction interacting with the river.
Groundwater Flow Direction
Knighton, Powys

## Slide 15
Groundwater Elevation vs River Teme Elevation (mAOD)
Location of Piezometers

## Slide 16: Groundwater Flow Analysis
Pragmatic.Expert.Solutions
@envireauwater
Using the groundwater discharge down the valley, the measured hydraulic gradient and the width of the gravel flow system, a check can be made to see if the transmissivity & resultant hydraulic conductivity are reasonable.
Darcy’s law : Q = Transmissivity (T) * i * w
T = 2,043,244/(0.0046*700*31*24*60*60)
T = 2.38m2/s
K = T/b
If b (aquifer thickness) = 30m
K = 7.92 x 10-3 m/s
Expected range = 1 x 10-4 to 1 x 10-2 m/s
ESI (2007) estimate 8.68 x 10-3 m/s
Hydraulic Gradient:
(140.25-137.75)/545
i =0.0046
Width of Gravels (150m contour)
= 700m
Validated Monthly Abstraction: 29,771m3/month
1.3% of water in the valley and 1.46% of groundwater
Month | Spot Flow Discharge (m3/month) | LowFlows2 Discharge (m3/month) | Difference (m3/month)
August | 249,466 | 2,292,710 | 2,043,244
Water in the
River
Water in the
Valley
Groundwater
(Bedrock and Gravel)
Comparison indicates that the values being used are appropriate

## Slide 17: Resource Impact
Pragmatic.Expert.Solutions
@envireauwater
Less than 1% impact on resource in a low flow month
Welsh Abstraction | Applied For Quantities in Application Ref: PAN-006555 and PAN-006557
Annual Abstraction (m3/yr) | 235,591
Average monthly Abstraction (m3/month) | 19,633
Average Daily Abstraction (m3/day) | 645
English Gravel | Accepted Quantities in Application Ref: NPS/NA/000956
Annual Abstraction (m3/yr) | 60,833
Average monthly Abstraction (m3/month) | 5,069
Average Daily Abstraction (m3/day) | 167
Total Abstraction from Groundwater | 
Total Annual Abstraction (m3/yr) | 296,424
Total Monthly Abstraction (m3/month) | 24,702
Total Daily Abstraction (m3/day) | 812
Waste Water Returns Permit Number: EPR/AB3697CN | 
Permitted Daily Discharge (m3/day) | 194.4
Total Annual Discharge (m3/yr) | 70,956
Net Abstraction from Groundwater | 
Annual Net Abstraction (m3/yr) | 225,468
Monthly Net Abstraction (m3/month) | 18,789
Net Abstraction as a Percentage of Water in the Valley at Lingen Bridge | 
Annually | 0.24%
Monthly* | 0.82%
* Using August as the month with lowest discharge
Notes: Lingen Bridge used as closest to Radnor. Buckton Bridge used in conceptual model and summary

## Slide 18: Summary
Pragmatic.Expert.Solutions
@envireauwater
The river experiences losses to underlying gravels as it flows from Knighton Bridge to Lingen Bridge
Environment Agency spot flow data shows that this pre-dates significant abstraction by Radnor Hills
By Buckton the gravels have discharged flows back to the river
The river subsequently dries up again just upstream of Leintwardine
The river would be expected to be naturally ephemeral due to the high permeability of the gravel substrate
The gravel fills a deep valley in the underlying bedrock
Runoff from hills recharges gravel valley fill
The gravel conveys water from the catchment down the valley
Use of LowFlows2 provides a value for the discharge from the valley (river + groundwater)
Use of spot flow data gives discharge from the river
Comparison of groundwater discharge (valley – river) results in valid value of gravel permeability
Groundwater flux can be compared to validated abstraction volumes in the application

## Slide 19: Conceptual Model
Pragmatic.Expert.Solutions
@envireauwater
* LowFlows2
# Site Data
** at Lingen Bridge
River Teme
Gravel fill
Flow return to river where gravel thins (decrease in T)
Small contribution from bedrock
Runoff to gravel recharge
Losses to gravel
Water in the Valley at Knighton
*August : 2,292,710m3
Groundwater
*August : 2,043,244m3
Net Groundwater Abstraction
#18,789m3 0.82%**
Water in the Valley at
Buckton Bridge
*August : 2,319,494m3

## Slide 20: Conclusions
Pragmatic.Expert.Solutions
@envireauwater
The River Teme SSSI is naturally ephemeral
River Teme flow accounts for only 13% of water in the valley during low flows
Groundwater flow through the gravels makes up a large proportion of the flow ~87%
At Buckton Bridge, the gravel flow has returned to the river, therefore flow to downstream SSSI is restored and no risk of impact from Radnor Hills further downstream
The net abstraction by Radnor represents only 0.24% of the annual valley discharge
Knighton STW discharges 910 m3/day (332,377 m3/year) compared to valley flow of 94,008,816 m3 (0.35%). Radnor’s abstraction of 0.24% of the annual flow.
Local groundwater contours show no impact from abstraction on River Teme SSSI
Abstraction does not effect SSSI flows because zone of influence does not induce direct flow from the river
Groundwater flow is down the valley NOT into the SSSI
Radnor Hills abstraction has no material effect on resource availability (<0.25%) & therefore no material impact on SSSI
Radnor Hills abstraction is no risk to SAC as SAC is in a different catchment
In combination risk only relevant from other GROUNDWATER abstraction
Other groundwater abstraction would have to be large to make a material impact
Other groundwater abstractors could effect river flow, but Radnor Hills would not contribute to an in combination impact