## Report
Biffa Waste Services
Trecatti Landfill Site
Annual Monitoring Review
January - December 2021
As required by condition 4.2.1 of Permit RP3733PC/V011 for Trecatti Landfill, the operator is required to complete an annual review of monitoring data.
The annual review will be based upon the monitoring results that the permit requires the Operator to undertake, which for the purposes of this report will run from January to December 2021. Biffa's monitoring is either carried out by ourselves, Lucideon or ALS laboratories. Biogene's surface water testing is carried out by Chemtest.
The review is split into 6 sections;
1. Surface Water
2. Leachate/Treated Effluent
3. Groundwater
4. Landfill Gas
5. Dust and Asbestos monitoring
6. Biogene
Capacity at Trecatti
Between January 2021– January 2022, 120,895m3 of void has been consumed, with the remaining void in January 2022 calculated as approximately 5,429,946m3 for the site to be completed to final levels.
Settlement Behaviour
The landfill settlement over the last year at Trecatti Landfill shows an average of 0.560m across the site. Modelling of the settlement of landfilled waste, both in duration and quantum, is difficult to complete with any certainty due to the complex and variable parameters that contribute to the settlement process. Settlement in landfilled waste is subject to a number of factors, including loading, type of waste, depth of waste and other processes including chemical and microbial actions. These processes appear as time-dependent, and are also influenced by factors such as leachate composition, pH, temperature and moisture. The settlement of waste over time comprises of two main elements: Primary or immediate settlement - this is load related and primary drivers are the expulsion of air and liquid from the waste resulting in consolidation. The rate of settlement is dependent on the depth of waste and the type of waste (and the amount of air/liquid contained therein). This is active during waste filling and immediately following completion of waste tipping. Secondary settlement – this is typically considered following post closure or cessation of tipping, and is initially a product of physio-chemical and mechanical creep (deformation due to load stresses) and then biological decomposition of the waste. These actions result in slow gradual settlement over a long period of time, typically many decades. Landfill settlement, due to the aforementioned factors, does vary considerably and can be as high as 40%.
1. Surface Water
The permit requires surface water discharge to be sampled and recorded monthly and to test for the following contaminants:
pH / Suspended Solids / Ammoniacal Nitrogen / COD
Following an Environment Agency audit on surface water management carried out on 16th May 2008, and subsequently approved on 30th July 2008, the
monitoring points have been amended as follows:
· SWA (81702001) – North Western boundary downstream discharge point
· SWB (81702002) – Eastern boundary downstream discharge point
· SWC (81702003) – Northern boundary upstream monitoring point
During the audit it was agreed that as the operator is unable to control the external influences on all four monitoring points that the rate of flow and volume measurement limit requirements on all three points would be removed. However volume of surface water pumped off site to the discharge point SWA would be reported.
Between January - December 2021 approximately 190,395m3 of surface water was pumped off site.
The following graphs represent the trends in the surface water quality for the period
All surface water stays under compliance consistently for the discharge limits of Ammonia, COD and Ph. There has been variuous incideance of suspened soilds triggering. All the surface water points are influenced by the neighbouring argrucultural land and therefore are not a reprentative of the sites surface water quality.
• All permanent engineering works (lining and capping/restoration) will continue to consider the impact of the works on surface water management during the design, construction and post-construction stages. This will include the provision of temporary storage lagoons, bunds, rain-flaps, ditches and pumping stations and pipelines. All permanent construction work will be the subject of independent CQA supervision. • All temporary engineering works (temporary capping) will consider the impact of surface water and may require the construction of rain-flaps and lined ditches to shed uncontaminated surface water into perimeter drainage ditches or temporary storage lagoons. • In order to reduce the build up of suspended solids within surface water bodies and water courses, any bare soil flanks and restored areas will be seeded with a suitable grass mix as soon as practicable in order to stabilise flanks, encourage infiltration and reduce surface run-off. This will be inspected and reseeded if necessary. • Spot sampling will be undertaken by the ECA in the site laboratory prior to any surface water being pumped to the perimeter ditch. • V-notch weirs are installed upstream of the surface water discharge points in order to slow down the flow of water to encourage the settlement of suspended solids prior to discharge. These features will be cleaned and maintained on a quarterly basis, and recorded on the critical plant schedule. • Perimeter surface water ditches, lagoons and other site drainage outlets will be inspected on a weekly basis and recorded in the site diary. •Road sweeper to be employed a minimum of twice a week. On periods of increased activity or poor weather conditions a road sweeper will be used more frequently or when the wheel wash is non-operational for a long period. This is left to the manager’s discretion. • Site to have a fully operational wheel wash, which will be cleaned every six months. A spare wheel wash pump will be held at site to replace immediately if the current pump fails reducing down time. The wheel wash is part of the critical plant list, which is reviewed monthly to ensure it is maintained as per schedule. The wheel wash may be cleaned more frequently depending on the manager’s findings during his/her monthly compliance inspection. All site users driving vehicles are instructed that they must use this facility before leaving site. Persistent misuse of the wheel wash by lorry drivers will lead to the driver being banned. • All waste vehicles must be sheeted upon arrival at Trecatti. De-sheeting must only take place in designated de-sheeting bay. • Vehicle check areas must be used by all drivers before leaving site so they can clean any excessive debris off their vehicles and remove any stones which may have been caught within their tyres whilst travelling over site.
2. Leachate
Leachate wells
The permit requires the Operator to sample leachate quarterly for the following components;
pH / Ammoniacal Nitrogen / Chloride / Total Alkalinity / BOD / COD / TOC / TON / Iron / Chromium / Copper / Lead / Zinc / Nickel / Cadmium / Magnesium / Potassium /
Sulphate / Calcium / Sodium / Manganese / Mecoprop / Toluene / Xylene / Naphthalene.
The permit also requires an annual suite to include the parameters above and hazardous substances
Leachate was sampled in February, May and September 2020 and annual components analysed for in November 2020. There are however no limits set up in the permit with which the leachate samples must comply, but they have been reviewed and are as expected.
The permit requires the operator to report leachate levels from specified points at monthly intervals. This data has been sent with the quarter report, below are graphs to look at the trends.
Leachate Well | Dip to base (m) | Between January and December, the majority of leachate wells on site have remained within the site compliance of 33m (for wells LW1, LW2, LW3, LW4, LW7 & LW8) and 5m (LW5 & LW6). Throughout 2021, the wells and pumps were serviced to ensure optimum leachate extraction. All the wells have electric pumps as they have been found to be more efficient and less prone to breakdowns at Trecatti. Wells 4 and 8 were above complaince in Novemeber and well 4 in December. As the site progress with operations in these areas the wells have undergone interruptions in there pumping regimes.
1 | 71.8
2 | 59.69
3 | 46.34
4 | 43.8
5 | 30
6 | 30
7 | 50.76
8 | 48
Treated Effluent
During this period 74,411m3 of treated leachate was released to the sewer.
The treated effluent is sampled and recorded monthly and tested for the following determinants:
pH / Suspended Solids / Ammoniacal Nitrogen / Temperature / Total Metals / Cyanide / Sulphide / Sulphate
The following results were recorded for the period:
Parameter 81703400 | pH | Suspended Solids | Ammoniacal Nitrogen | Temperature | Total Metals | Cyanide | Sulphide | Sulphate | Oil / Petroleum Spirit
Discharge Limit | 6-11 | 400 mg/l | 40 mg/l | 43oC | 2 mg/l | 1 mg/l | 2 mg/l | 1000 mg/l | Nil
Jan | 7.4 | - | 0.44 | 21.4 | 0.53 | 0.043 | <0.020 | 83.4 | Nil
Feb | 7 | 93 | <0.41 | 21.7 | 0.465 | 0.034 | 0.025 | 157 | Nil
Mar | 6.9 | 21 | 1.16 | 24.8 | 0.53 | 0.029 | <0.020 | 101 | Nil
Apr | 7.6 | 12 | 0.43 | 23.1 | 1.4 | 0.038 | <0.020 | 100 | Nil
May | 7.1 | 20 | 1.28 | 26.8 | 0.19 | 0.041 | 0.054 | 102 | Nil
Jun | 7.9 | 126 | 3.25 | 27.9 | 0.15 | 0.057 | 0.041 | 97.2 | Nil
Jul | 7.4 | 35 | 8.48 | 25.7 | 0.17 | 0.053 | 0.028 | 92.1 | Nil
Aug | 7.6 | 36 | 0.5 | 26.9 | 0.14 | 0.039 | 0.025 | 100 | Nil
Sep | No sample taken- Power Outage
Oct | 7.7 | 57 | <0.41 | 19.9 | 0.12 | 0.017 | 0.0232 | 144 | Nil
Nov | 7.3 | 56 | <0.41 | 20.9 | 0.16 | 0.016 | <0.01 | 85.5 | Nil
Dec | 7.3 | 52 | <0.41 | 21.9 | 0.13 | 0.025 | 0.0196 | 119 | Nil
All parameters are within the discharge consent limits. The temperatures were not taken at the time of sampling in January due to equipment failure.
3. Ground Water
Annual and Quarterly samples were recovered from groundwater boreholes: GW1, GW2, GW4, GW6, GW8, GW11 and GW12 during this period.
The boreholes with compliance limits associated with them are GW1, GW2, GW9, GW10, GW11, and GW12
In addition the compliance limits have also been assessed for GW13 and were proposed in the 2014 annual report.
Groundwater Trends 2019-2021
|  | Ammonia | [6 empty] | Chloride |  | 2016-11-22
|  | Mecoprop | [6 empty] | Cadmium
Naphathelene
In the above graphs the boreholes GW3, GW5, GW7, GW9, GW10, GW11 and GW13 have been excluded from the graphs due to insufficient data. Where a result has been reported as less than the limit of the laboratory detection limit i.e <0.41mg/l this is shown on the graphs as 0.41mg/l
From the above results, one groundwater borehole exceeded the compliance limits for ammonia
GW2 saw a result of 17.7mg/l ammonia during Febraury.Overall the results indicate a falling trend. The other boreholes remain stable.
Chloride levels have demonstrated a stable trends. Except GW6, GW8 and more recnetly GW4 these boreholes do not have compliance limits. These boreholes are upgradient of the site and may be influenced by the neightbouring quarry extraction.
All Mecoprop levels remain steady and GW2 continues to have a decreasing trend.
Cadmium and Naphathalene levels have remained under compliance limits and are stable compared with previous year results.
To summarise some groundwater wells have experienced very low groundwater levels and slow recharge rates meaning that samples could not be taken from GW3, GW5, GW7, GW9, GW10 GW11 and GW13 throughout the period. All boreholes that could be sampled continue to show stable trends.
Trends from the above graph show that many of the groundwater boreholes show minimal variation between January 2019 to December 2020. However there have been various peaks throughout the year which may be influenced by the neighbouring quarry extraction.
4. Landfill Gas
FID
| Parameter | FID (Max ppm)
| Jan | 35
| Feb | 20
| Mar | 30
| Apr | 20
| May | 10
| Jun | 10
| Jul | 20
| Aug | 20
| Sep | 12
| Oct | 8
| Nov | 8
| Dec | 6
The site continues to pro-actively monitor surface emissions and the gas extraction system. Routine reviews of this data leads to the installation of temporary capping and gas infrastructure improvements to capture as much landfill gas as possible from the site. All complaints during this period were investigated with a FID Gastec around the site perimeter and supplemented with olfactory surveys at the receptors to identify the source of the odour. The number of odour complaints continues to remain low.
External Borehole Monitoring
At present there are twenty-six external boreholes located on the outer perimeter of the site. All readings have been submitted in the quarterly reports.
An update to IC8 was submitted in January 2013 and a final version was agreed in April 2013 and compliance and action limits changed as identified in CAR form date 24/04/13
As is well documented for the site there are old mine workings and current mine workings in the locality of the site which make the ground gas around the site complex. This coupled
with the old council run Merthyr Waste site adjacent to the current lined Biffa Site make the issue of gas migration in perimeter boreholes difficult to attribute to one specific source.
The gas extraction system is fully maintained, monitored and infrastructure added frequently to ensure the maximum flow off site through the engines and flares is maintained.
Below are graphs showing the methane and carbon dioxide percentages for the gas boreholes which exceeded compliance limits between January and December 2021, gas boreholes: GB4, GB20, and GB22. All boreholes show trends during the year that are generally compliant with historical levels. Where there has been incidences of levels above compliance this has not been associated with raising trends, therefore no deterioration in the gas extraction system of site.
Gas Compound
Site | LFG flared (M3) | LFG used in engines (M3)
Trecatti Total | 493231 | 14214554
5. Dust & Asbestos Monitoring
Dust monitoring is carried out in four locations and Asbestos at six locations every 6 months at the site.
Measurements are taken for total inhalable dust and Particulate matter <10 microns.
The results are collected over a 24 hour mean using a portable meter or equivalent.
Analysis was conducted in June and December for Deposited Dust Monitoring & PM10 by ALS and the results are as follows:
PM10 Results
|  | D1 Filter | D2 Filter | D3 Filter | D4 Filter |  |  | D1 Filter | D2 Filter | D3 Filter | D4 Filter
| Date out | 2021-06-21 | 2021-06-21 | 2021-06-21 | 2021-06-21 |  | Date out | 2021-12-14 | 2021-12-14 | 2021-12-14 | 2021-12-14
| Date In | 2021-06-22 | 2021-06-22 | 2021-06-22 | 2021-06-22 |  | Date In | 2021-12-15 | 2021-12-15 | 2021-12-15 | 2021-12-15
| Particulate Matter <10 Microns (mg/m3) | 9.5 | 11 | 9.7 | 2.7 |  | Particulate Matter <10 Microns (mg/m3) | <0.0 | <0.0 | <0.0 | <0.0
Deposited Dust
Results |  | D1 Filter | D2 Filter | D3 Filter | D4 Filter |  |  | D1 Filter | D2 Filter | D3 Filter | D4 Filter
| Date out | 2021-06-21 | 2021-06-21 | 2021-06-21 | 2021-06-21 |  | Date out | 2021-12-14 | 2021-12-14 | 2021-12-14 | 2021-12-14
| Date In | 2021-06-22 | 2021-06-22 | 2021-06-22 | 2021-06-22 |  | Date In | 2021-12-15 | 2021-12-15 | 2021-12-15 | 2021-12-15
| Deposited dust, mg/m2/day | 340 | 390 | 220 | 860 |  | Deposited dust, mg/m2/day | 67 | 610 | 82 | 17
There are 4 Monitoring locations for this Monitoring - D1, D2, D3 & D4
Deposited dust results were above the compliance limits in June at all locations and D2 in December, this is thought be be contributed to an offsite source.
All particulate matter locations were under compliance limits.
Analysis was conducted in May and Decembers for Asbestos Monitoring by Lucion and the results are as follows:
Asbestos Monitoring Results
2021-05-05
Sample | Start |  | End |  | Fibres (N) | Reported Result
| Time | Flow (l/min) | Time | Flow (l/min) |  | Fibres cm-3
D1 | 9:25 | 8 | 10:33 | 8 | 2 | <0.01
D2 | 9:30 | 8 | 10:36 | 8 | 2.5 | <0.01
D3 | 9:35 | 8 | 10:40 | 8 | 1.5 | <0.01
D4 | 9:40 | 8 | 10:43 | 8 | 2 | <0.01
D5 | 9:51 | 8 | 10:51 | 8 | 3 | <0.01
2021-12-14
Sample | Start |  | End |  | Fibres (N) | Reported Result
| Time | Flow (l/min) | Time | Flow (l/min) |  | Fibres cm-3
D1 | 10:26 | 10 | 11:16 | 10 | 1 | <0.01
D2 | 10:29 | 10 | 11:19 | 10 | 2 | <0.01
D3 | 10:32 | 10 | 11:22 | 10 | 1.5 | <0.01
D4 | 10:37 | 10 | 11:27 | 10 | 1.5 | <0.01
D5 | 11:30 | 10 | 12:29 | 10 | 1.5 | <0.01
D6 | 11:33 | 10 | 12:31 | 10 | 1 | <0.01
None of the above sample locations breached the asbestos fibre limit
6. Biogene
Biogenie started operations at Trecatti in September 2018.
As stated in permit variation V011, there are two Surface Water Monitoring Points that require analysis to comply with the requirements of this Permit.
Biogenie send their samples of the required areas on a monthly basis to Chemtest for analysis. All data has been included in the quarterly reports.
Pumping Permits are raised by Biogenie and authorised by Biffa Personnel when they want to pump from SW 2 Lagoon into the 385 Lagoon and is signed off
by Biffa only when the process water is compliant. Any non compliant water is sent to sewer.
SW2 has now been integrated into the biogenie water treatment system, therefore only one sample is taken for the system.

## Complaints
Year | No. of compliants
2000 | 244
2001 | 1082
2002 | 782
2003 | 422
2004 | 206
2005 | 191
2006 | 296
2007 | 702
2008 | 101
2009 | 25
2010 | 28
2011 | 65
2012 | 78
2013 | 22
2014 | 77
2015 | 62
2016 | 6
2017 | 5
2018 | 4
2019 | 2
2020 | 4
2021 | 5

## Table S4.3
Table S4.3 Performance Parameters
Parameter | Frequency of assessment | Annual Total | Unit
Water usage |  | 2094 | tonnes
Energy used including leachate treatment |  | 1090.8944 | MWh
Total raw material used |  | 1110 | tonnes
* Raw materials - wood fines used as soil enhancer in STF

## Table S4.2
Table S4.2: Annual Production/treatment
Leachate | Cubic metres/year
Disposed of off site | 0
Disposed of onsite effluent treatment plant | 74411 | m3
recirculated into waste mass | no recirculation N/A
Surface water and/or groundwater | Cubic metres/year
Disposed of off site | 190395 | m3
Disposed of to effluent treatment plant | 0 | m3
landfill gas | Cubic metres/year
combustion in flares | 493231 | m3
combustion in gas engines | 14214554 | m3
other methods of gas utilisation | N/A