## Slide 1
Mekatek Ltd – Amex Park -West side of site
ADMIN STORAGE
DUST ROOM
SHRED & WASH
BALER ROOM
MAINTENANCE
Seg room 2
SEG ROOM1
PBM Building
Main OFFICE
ONWARD PROCESSING STORAGE
STORAGE
W/S
STORES
WORKER SERVICES
PAD
PAD
MBG SUB 1
MBG SUB 2
Cow & Gate SUB
Llanstephan road SUB
MBG SUB 3 & Old Pump Station
WEIGHBRIDGE
OIL BAY
STORAGE
TRANSFER STATION
Seg room3
Buildings
Boiler House
UF Filter Room
Switch Room
Skip
Sub Station
Silo, Tank
1
2
3
Building Access/Exits
Fire Extinguishers
Off site Emergency Information pack
Emergency Assembly Point
Weighbridge
Spillage Kits

## Slide 2
OIL PROCESSING
D
ACCESS RAMP
OT 2
OT 1
ST 1
ST 2
DC 1
DC 2
UF 1
UF 2
OT 3
OT 4
OT 8
OT 6
BOILER HOUSE
OT 5
OT 7
OT 9
CT
Switch Room
LAB

## Slide 3
OIL BAY TANK KEY |  | 
TANK ID | TANK DETAIL | TANK MONITORING & CONTROL MEASURES
OT 1 | 60,000 gallon vertical cylindrical tank. Mild steel construction nominal 6mm wall thickness. Fixed position. | Float level indicator on tank. Visual inspection daily and when filled/emptied.
OT 2 | 60,000 gallon vertical cylindrical tank. Mild steel construction nominal 6mm wall thickness. Fixed position. | Float level indicator on tank. Site Glass to be installed (Aug 2022) Visual inspection daily and when filled/emptied.
OT 3 | 3,300 gallon horizontal tank. Stainless steel construction nominal 4mm wall thickness. | Daily visual inspection using inspection hatch on top of tank.
OT 4 | 6,000 gallon vertical cylindrical tank. Mild steel construction nominal 6mm wall thickness. Insulated with glass fibre insulation. | Electronic Float level indicator including pump level regulator and cut off switch
OT 5 | 13,000 gallon horizontal cylindrical tank. Helically wound construction nominal 12mm wall thickness. | Float level indicator on tank. Visual inspection daily and when filled/emptied.
OT 6 | 6,000 gallon vertical cylindrical tank. Mild steel construction nominal 6mm wall thickness. Insulated with glass fibre insulation. | Visual inspection daily via hatch when filled/emptied Float level indicator to be installed August 2022
OT 7 | 1,000 gallon vertical cylindrical tank Stainless steel construction nominal 5mm wall thickness Insulated with EPS | Daily visual inspection using site glass on tank
OT 8 | 8,000 gallon horizontal cylindrical tank Mild steel construction nominal wall thickness 8mm | Daily visual inspection using site glass on tank
ST 1 | 33,000 litres above ground separator tank. | Automatic overflow of water into ST2
ST 2 | 33,000 litres above ground separator tank. | Automatic overflow of water to Effluent Plant.
DC 1 | Modified skip discharge container. | Open tank visual inspection daily and when filled/emptied.
DC 2 | Modified skip discharge container. | Open tank visual inspection daily and when filled/emptied

## Slide 4
LORRY PARKING
Mekatek Ltd – Amex Park - East side of site Effluent Plant
1
2
3
4
Buildings
Small Pump House
Screw Press Building
Small substation – Plant Control Room
Lab
5 Boiler House
Silo, Calorifier or Effluent Tank.
Bunkers
Building Access/Exits
Fire Extinguishers
Quarantine Areas
Emergency Assembly Point
Spillage Kit
5

## Slide 5
EFLUENT TREATMENT TANK & VESSEL KEY |  | 
TANK ID | TANK DETAIL | TANK MONITORING & CONTROL MEASURES
 | 60,000 gallon concrete tanks. Storage and treatment | AM visual inspection of tank condition & levels. Levels reviewed against known inputs for the day. Visual monitoring during discharge process. Weekly management inspection of tanks
 | 60,000 gallon conical clarifier tanks. Treatment | Weir system process plant, designed not to overflow Visual inspection of tank condition & levels Weekly management inspection
 | 45,000 gallon conical clarifier tanks. Treatment | Weir system process plant, designed not to overflow Visual inspection of tank condition & levels Weekly management inspection
 | 500,000 gallon bunded glass fused storage tank. Storage only – bunded and lidded. | Double skinned tank. Ultra Sonic Level Monitoring system, with alarm and auto cut off of intake. Daily inspection of level via monitoring system. Weekly inspection of level between skins of tank. Weekly management inspection of tanks
 | 150,000 gallon sequential batch reactors. Glass fused. Treatment | Ultra Sonic Level Monitoring system AM inspection of level via monitoring system. PM visual inspection of top of tank. Inspection of level via monitoring system when tank is filled or emptied. Bio reaction (Foam) auto cut off technology Weekly maintenance inspection Weekly management Inspection of tanks