[9 empty] | 㜸〱捤㝤〷㜸ㄴ搵晡㝥㑥㐸㤶㑣㈸㔹㐵〵ㄵ㌰ㄴ㤵愲㐸攸愰昴㕥愴㠵㘶㡤㑢戲㈱㠱ㄴ㐸㌶ㄴ㐵〵㐴挰㝡敤〲㉡㘰〱ㅢ敡戵㠳㌵愲㈸㉡㌶戰㜷戸㘲挳㝥敤昵晦扥摦捣㔹捥㤴摤攴攷晦收㜹㕣挹攷昹晡㌷敦㌷㌳㍢㌳㝢捥㙥㡡㑡㐹㐹昹ぢ㉦晥㥦慦㌴づ㥡攷㉥愸㡣㐵㑢㍢つ㉥㉦㈹㠹收挷㡡换换㉡㍢つ慣愸㠸㉣ㄸ㔳㕣ㄹ慢〷㠳㔰㕥㌱昴㤵改㜹㤵挵愷㐷㌳昲收㐶㉢㉡㘱㤴㥥㤲㤲㤱㘱愵㐲㝦戰昳ㄷ搶㡣㐵㉦㉢㡤〴㔶㈹㔶㠸愴㍥㐹〶㠹㐵㤲㐹搲㠰愴㈱㐹㈳㤲挶㈴㔹㈴㘱㤲晤㐸昶㈷㘹㐲㜲〰挹㠱㈴〷㤱㌴㈵㘹㐶挲晣搶㈱㈴㠷㠲㌴㙣づ㌲㘹昰愰㜱搳㘷㘲㙢㜲㘳攵ㄵ搱愳戲愷搸㌵昷捤挹改㤴搳愹㑢搷摥㌹㥤㍡ㅦ㤵㍤戸慡㈴㔶㔵ㄱ敤㕢ㄶ慤㡡㔵㐴㑡㡥捡ㅥ㕦㌵扤愴㌸㝦㜴㜴挱愴昲㔹搱戲扥搱改㥤扢㑥㡦㜴敢㤵搳慤㝢昷挲摥扤㝢㌵㙣㠱挸㘳〷てㅡ㕦ㄱ㉤慣晣㕦挵㙣挹㤸攳〶て敡㌴㌶ㅡ晢㕦挵㍣っ㌱ㄱ㜲㐸㜹㘹愴戸散㝦ㄴ㌴㥤㍤敤㍡㈴㥡㕦捣收㐷愳ㄵ挵㘵㌳㍡愱㙣ㄷ搰攰㝡㜶ㅡ〶挴昳㈳㤵戱挱搱㤲㤲㠹搱㐲昶扤㘱㈹㌱㡢㔶㐴换昲愳㤵㡤㑢㠷捥捦㡦㤶㌸敡捡㡣搲㈹㤱㡡戱㤱搲㘸ㅡ〷㔹愵㜶摦㐶ㄶ㐴换㘲挵戱〵㡤㑡㈷㔷㐶㈷㐶捡㘶㐴㘹㤲㕥㍡扣慡戸㈰㉤㑤愵愵愵搴㍢㌲愸ㄸ改㑤愷㘱ㄵ昹㠳㡢㈲ㄵ㌱攱搸戵㥣㈰㕢㘳て㤱挲㕤㘵㜱㉦捡昶㜸戱㑤戹挵愵愳愳ㄵ㘵搱ㄲ㈶㘱昳㍡㝡㡣〴ㄳㅢ晡㌸㌸㝡㙢搸ㄸ搵挰㌹摥戸㈹捣㘲㘵㤳戴〲〹戵〶㌹㜲㔲㐵愴慣㜲搰愴扣昱㤱㔸㔱㑥㑥摥攰昲戲晣扣摣搹〰㍥㕡搹㍤㙦㔲㜱㘹戴ㄲ㍢㘹戴㤷搵㠶㙥㙤㐱㔴摡㍢㌸愶捤戰㍣慥㔲昳㈲愹㜹搳㔳昳昲㔳昳ち㔲昳愲愹㜹㠵愹㜹㌳㔲昳㡡㔲昳㡡㔳昳㘶愶收捤㠲㡤㝥㘵搴慦㥦敡扣扥戹晣㥥晢㙥㕤㥡㌵㘶昵㔹摦慦㝥戴攸㥣捦ㄴて㘳㌹㥥㡦挰挰㍡ㄲ㈴搴づ㈴㔹㤹㍤昶㤵搹捤㙡㑦户づ㈰㑡扤㠶㌲㔹敡㠹昷晦㤴扡戱㔱㥦愱㤷㌵㝤㘱挳戹挳㜷㘴㉡㥥㈵㈴挷㔱㌴㍥ㅡ㈴搴〹㈴㔹㡥㉥晢㜲昴戶㡥愱㕢㘷㄰愵㕥㜲㜲㕣㝥捥散晣㝥㜷摤㍣攰㥥㠵ㅢ摢敥摣昱搰ㅥ挵㤳㤰攴攸㐲攳慥㈰愱㙥㈰挹㜲㜴摤㤷愳㤷搵㥤㙥㍤㐰㤴㝡搶挹㌱晣慡㐸扤㌹㠵㘹㘳㉥㔷戹㡤㐶慣㈹捦㔵摣搷㈵㐷㉦ㅡ昷〶〹昵〱愹㘵㡥摥搶戱㜴㍢づ㐴愹㈷㥤ㅣ戹慦㠶捦㍢㘷攴敥㈱昷ㅦ㜶㑡㑡㠳昵ㅤ慥㔲㍣㠵㑡㡥㝥㌴敥てㄲㅡ〰㤲㉣㠷戱摢昴戶〶搲㙤㄰㠸㔲㡦㍡㌹扥ㅣ㕤㝡摡敥昶攷っ摡ㄴ扥攸散㡤摢㥢㌷㔷㍣㐳㑢㡥㈱㌴ㅥちㄲㅡ〶搲㉥挹慥㘹昴㈳愷戳㌵㥣㝥㈳㐰㤴㝡搰㐹昲搱愴㉢挲敦㔶づㅢ戸昴挱㍦㕡慦㍤昰㤱づ㡡敦〰㤲㘴ㄴ㡤㐷㠳㠴挶㠰㈴摢㤰㥥晢ㅡ搲摤㍡㥥㙥㘳㐱㤴扡摢挹㌱昸敤捥㌷㙤㍤敦捦攱㤷㌶㕡㌵昹㡡昳㤷ㅥ愷㜸㈰㐸㡥昱㌴㥥〰ㄲ㥡〸㤲㉣㠷戱昳昶戲㜲改㌶〹㐴愹摢㥤ㅣ〷昷扦攰慢敤㕢㝦ㅥ㜳晥㠶㥣昶㌳ㅦ改昳㠴攲晢㤷攴㤸㐲攳愹㈰愱㘹㈰挹挰㌲戶〳㘰㥤㐰扦ㄳ㐱㤴㕡敦㈴㌹攵挴捡㔸捥敢㐳㠶摤昴㐷晢㕢㡦㝤㘵捥㘷㡡敦㡦㤲攴㘴ㅡ㥦〲ㄲ㍡ㄵ㈴搹㠶㜴摢〷㔶㉦㉢㡦㙥愷㠱㈸戵搶挹昱敥㠸扢㥦㍥㘵捡㔳㐳㤶っ〸摤㍥慡昹敦晢㈹扥晤㑡㡥改ㄸ㔸昹㈰愱〲㤰㘴ㅢ㘲ㅣ㈱搸㤰㈸晤ち㐱㤴㕡攵㈴戹晦户㝡愷㥤ㄹ敢㌱昸㠱摢㑢㔲㔶攵ㅤ摤㑦昱敤㕤㤲ㄴ搱戸ㄸ㈴㌴ㄳ愴㤶ㅢ搲摢攲㘹换㉡〱㔱敡㜲㈷挷㜲㙢摢搴㤲㝢㍥ㅢ㜸敥搸㈷摦㝣晢㡡捦摢㈹㕥㍤㐸㡥㌲ㅡ㤷㠳㠴㘶㠳㈴换㤱戳て慣㥥搶ㅣ扡㔵㠰㈸㜵㤱㤳㘳晣ㄱ慤㠷㝤晤摡捣㌱敢㍦㔴敤㥦㔴㥦摣愶㜸㜱㈲㌹㘲㌴慥〲〹捤〵㐹㤶挳攸㝡㉦㙢ㅥ摤收㠳㈸戵摣挹ㄱ昹㉡㝡摤挴㡥捦つ扡攳㤹ㅤ㥦㥤㍦晣扥㐵㡡搷㍥㤲攳㜴ㅡ㥦〱ㄲ㕡〸㤲慣㈱挶摥㡢㠶㥣㐹扦戳㐰㤴㕡散㈴㜹愵戴攳㔳慦㝤搳㘶搸收㝥ㅦ晥摣昱挰㌷㝡㉢㕥㕢㐹㤲㐵㌴㕥っㄲ㕡〲㤲㙣㐳㡣昳㐹㑦敢ㅣ扡㉤〵㔱敡っ㈷㐷㡢捤㐷㌵捥晤戵捦搰㙢㥥㔸昷㘱扢㙢摢㌷㔴扣㜴㤳ㅣ换㘸扣ㅣ㈴戴〲㈴㔹づ㘳㐳㝡㕢攷搱敤㝣㄰愵慡㥣ㅣ㤷愵㜴㤸昹㘷㤳搴攳ㅦ㝣㝥攸㔵挳㙥㕤摦㔶昱捡㔰㜲㕣㐸攳㡢㐰㐲ㄷ㠳㈴换㘱㥣戳㝡㔹晦愲摢㈵㈰㑡㤵㍢㌹㌲㙥ㄹ㍢攸攳ㅢㅡ㡦扡㜱敤捥ㄳ㉦㙥㕡晦㕢挵ぢ㑦挹㜱ㄹ㡤㉦〷〹㕤〱㤲慣㈱〶㔶㘸挸㤵昴扢ち㐴愹㘲㈷挹敥敡搶㠳㍥晣㜰敦愸攵摢㙦攸㝡㙥摦扣ㅥ㡡ㄷ戶㤲㘴㈵㡤㔷㠱㠴㔶㠳㈴摢㄰㘳敦敤㙤㕤㐳户㙢㐱㤴捡㜷㜲攴㙣㕤昹攴㤷挷散ㅤ扤晥晡㑢㔶㡥晡戳敢㘲搵っ㙡挹戱㠶挶㙢㐱㐲敢㐰㤲㙤㠸㜱㍡挱㠶㕣㑦扦ㅢ㐰㤴㍡挵㐹昲挱愱ㅦ扣戸㜸昴攵㐳ㅦ晡㘸搱晥搷㝥搱晣㍣挵敢㜲㐹㜲ㄳ㡤搷㠳㠴㌶㠰㈴㑢㘲㙣〸㤲摣㑣扦㕢㐰㤴㥡敡㈴ㄹ㜸昸捥㥤㘷㍦戰㘷挰㡡㉥慢㔷户扥收搶㈵敡㄰愸㈵挹㙤㌴扥ㅤ㈴戴ㄱ㈴ㄹ㕡挶㐹慢愷㜵〷摤敥〴㔱㙡㠲㤳攳戵㉥㤹㉢ㄶ㥥戲㜲挸〳㑢㝡扦㝥攴昵㌷晦愲づ㠵㕡㜲晣㥢挶㜷㠳㠴敥〱㐹㤶挳㌸搶㝢㕢昷搲敤㍥㄰愵㐶㍢㌹戶愷㙣㡢敥㙣戳㘵散摡㡤敢㔶㝦昹挴慢㤷㌷㝣〰敡〹捥㤵攱㤰㡡挸㍣㕣㕥敦扢㜲敦搲愹㌳晦慢昹㤶〵㜷㉣㠵摤ぢ㝢ㄶ收攴ㄴ㜴敦ㅣ改ㅡ㐹捦㐶搸摡㕥㈸昳㈸㙤㔸㌸戵戸慣愰㝣㥥㕣㌹㌷㉣ㅣ㔶㕣ㄲ㡢㔶〸㤳㔵㠸晦搹㔷晦挲㌷㉡ㅣ㍡ㅦ户㑤昹昶㐵昶〱㠵㠳愳ㄵ㌱摣㙥挴ㄶ散扢昲㙥㍥㈸㔲ㄹ摤挷㜶㜴㘲て㉡慦㉡㉢愸㍣㌴㔸㤹ㅢ㡢挴愲㠷㜸㜵晢㠲昸摣㜲㜱㉢ㄲ慤㤴㤲㕡㝡摤愶㐴㑡慡愲〳攷ㄷ摢敡ㄶㅥ㌵㙥㑡捡愷㈷搶づ慢㠸捥㠹㙢㝤ㄵつ挴㥤昲㕣㠹敤摢㑡㕢㘵搷㤵㍤戸愸扣㌲㕡㈶攵㜵㉣ㅤ㕦㥣㍦㉢㕡㤱ㅢ攵㝤㜶戴㐰㌶昵㐰慡㥣㍢愳㡥攳捡戰愱戸搷㈹㘸㙤㑡〹㜴戴慣㈰㕡㠰㝡㘷〳攵〵㤳㈲搳㑢愲〷戹㑣散㥣㔰ㅣ散ㄲて㉢捦慦慡挴ㅤ㐴慣愲扣挴慤ㄹ㔸㌰㌷㠲扢戱㠲攳换ぢ愲㘹昲㑡戱愹㑡愹㔷㑦愹㤴㜶㐱户㌵㡣㕤挹ㅢㅦ㘳㈷攱敤㔵㜲㘳㘳㈷愲㜱攰つ㔳㍣㌲〶挶㑥㐶晢昶㐹㉢㌱㜷㐲㕡㜷㑥㙡ㅤ戰㤳搲愹㤹晢挰敢㌴ㄱ晤㐱ㅦ㑡愲㍣㉡㔳摢㈶づ戹㙦扦慣愱㔲愳㉢㝣慣㐲敢㈴愰㐹搸昸扥㔷户挶愹愹㑤㥣慤ㅦ㍡ㄷ昷摣㈳㈲㘵〵㈵搱㡡愴て㠵ㄴ㉢戲ㅥ㈴搹㐴戲㤹攴㈱㤲㠷㐱搲㠷攰ㅣ㤷㄰搱㌴㔸愸昹㙡㐱晡扣攲㠲㔸㔱愸㈸㕡㍣愳㈸〶ㄹㅥ㈶㘵㘴㄰㙥摦换㝡ㄴ㈲敢㌱㤲挷㐱㌲㌳㔳㐲搵昸㍦㐶搶ㄳ愴㤹㈹改慤昰晦晦晢㉤㝥㉡扣㉣㜹愲㠰㐷㍥㤵改愵㜸㜰㔱㔹慦㕥搰㤶㡦㠸㔴ㄶ挵㜸搰㈵㔷㌲摥ㄶ㤲㈷㐱ㅡ㍥〵㌲㜶㐴戴〴㠷散晦敡㘹㔱㝡ㅢ挴慣昱愹〴㉦ㅢて㉡捤㕤㔰㤶㕦㔴㔱㕥㠶㘷㜶㐳㈲戱挸挰㝣㍣㝡愹㔴㤱㔰改㤸昲挱㔵戱㔰改㠸㘲晣慦㘱改挴攸散㘸㈴㌶ㄸ愷攴㔸愳搲㌱㜸㙣㈳攷捣㤱〵昳搳㑢敤㈷㉥㐳愲㤵昹ㄶㅦ捤㡣挴㈹㘸㝥〸㈳㥣㔳ㅢ㤶昲愴ㄲ㥤ㅦ㘳攸晡愵攳㈳㜸戴ㄳ戳㘰搴㔱扣散ㄱ㍤ㅢ㠹㑣㝢㘷㍡ㅣ㈲㠴㘵㘸㐴㘹㈰〲㍢㔲ち昷ㄲ扣㕢攲㙤㌷捤愱摥愳㘵㜲慣戸愴戲㤳〳㙦愷㈱攵㜸㜴ㄷ㤵愷㤶㠴㍤ㄴ挲捥ㄴ㑡摡㉣敦㐱捤㘷㍢攳昲愷摢㘱㔱捡昰㡡昲慡搹㉤ㄱ敢㝦ㄵ㠷戱㔲慣慤㈰㙢扦扤敤搸挳慦扢敢㉦攷晦㘷攳㜰㤱㤷搵㥡ㄶ搵㈰㘴昱㍦㜹㔹摢昰扦捣㘴扡昴戶戰〸㍣慢㈶㜸っ㤵づ晢㠶愵搸摡㐹ㄵ㔱㜹慥㤶㈱捣㠲搹搱㐶愵㔳换㉢㘶㑤㉦㉦㥦挵收㌷ㄶ慥戲㈸ㅡ㡤昱㘱㔵〳攷搹ㅣ挷㑡愹㝡昵㕣㡦㥣㡣愷㕡㠷㈱㝥㘸㍢㐸愳㠱㈵㈵搹㍡㘲㘵攸〵㠸敡攱摤㈳昴㈲〶㠷昵攸摣戵㕢捦㐹扣戴改㤶摤㝤㔲㙥㜶捦捥搹戱昲散㥣捥㥤㍢㜷㥡㕦㔲㔹慡㜲〰〲㥦ㄶ㥤扣攳慦㙤敤㥥晤㜹昴㠶收昳㥦摦昵摢㠲㤵慡戳愳昰㍤慡㍡〲㘱戳昱㘷扤㐲戲㠳㘴㈷挹慢㈴慦㠱愸づ㜰攵改〹㘳昷换㝡〳扣昵㈶挹㕢㈰㌸愹㐸㈳〰晣㍢㌶慢㡥挴晦㜹㥥戱摥㈵㜹て㐴昱搱ㄶ㡦挸ㄴ敢㝤㤰㠴㙤㙤㐷㡢㙡㄰㈴㡥㘷戶㜶㐱㤰㘹㈵搱愹づ戰㘰㙢㉤㐲㘹ㄱ㍣㡢挰愹㘶〸ㄳ〸㑣㔳㐷攱㝢扥㜶ㄴ摣戲改晦㌹挹㕥㤲㉦㐸扥㈴昹ち㐴敤〷搷㘰㘰扥愱捤户㈴摦㠱ㄸ挰㝣㙦戳敡㘸晣㕦㠰昹㠱㐶㍦㠲愸㘳㐰㙣㘰㝥挲㈸㈱㌰㥤攸㔰つ㠲攴晢㠰昹ㄵ㠲㑣㉢㠹㑥㜵㠶㐵㄰㌰㝦晤㤹〰㤸㍦ㅤ㠵敦愱㘰ㄷ㐴捡挶㥦㔵㑦㠱昰攳㄰㉢㥤㈴㐴㔲ㅦ㐴晤っ搷㘰㘰㉣摡㘴㤲㌴〰㌱㠰㘹㘴戳慡㉢〲户㘲昰挶㌴捡〲㔱摤挱摡挰㠴挱㈶〴愶ㅢ扤慡㐱㕣挰㌴㠱㑢愶㤵㐴愷㝡挰㈵〸㤸㡦ㄳ〱戳挷㔱昸㥥㘴昶㐲愴㙣晣㔹捤㤱搴㙡㐱搲㤲攴㌰㤲㙣㄰昵㐱㐲㘰㕡搳愶つ㐹㕢㄰〳㤸㈳㙣㔶昵㐶攰㔶っ㝥㈴㡤摡㠱愸㘳挱摡挰戴〷㥢㄰㤸㍥昴慡〶㜱〱㜳ㄴ㕣㌲慤㈴㍡㜵ㅣ㕣㠲㠰㜹㈱ㄱ㌰摢ㅤ㠵敦昱㙢㍦㐴捡挶㥦搵ㅤ㐹慤ㅥ㈴㍤㐹㝡㤱昴〶㔱㑦㈷〴收㔸摡ㅣ㐷搲ㄷ挴〰愶扦捤慡晥〸摣㡡挱〷搰㘸㈰㠸ㅡ〸搶〶㘶㄰搸㠴挰っ愰㔷㌵㠸ぢ㤸愱㜰挹戴㤲攸搴㈰戸〴〱㜳㕦㈲㘰敥㜵ㄴ扥㘷挶㐳㄰㈹ㅢ㝦搶㔸㈴戵挶㤱㡣㈷㤹㐰㌲ㄱ㐴摤㤱㄰㤸㐹戴㤹㑣㌲〵挴〰㘶㥡捤慡愱〸摣㡡挱㑦愰搱㠹㈰㡡㡦㤸㙤㘰㑥〲㥢㄰㤸㘱昴慡〶㜱〱㜳㉡㕣㌲慤㈴㍡㌵〲㉥㐱挰㕣㤳〸㤸搵㡥挲昷㥣㝢ㄴ㈲㘵攳捦㥡㠱愴㔶ㄱ㐹㌱挹㑣㤲㔹㈰敡㡡㠴挰㤴搲愶㡣愴ㅣ挴〰㘶㡥捤慡搱〸摣㡡挱㉢㘸㔴〹愲㡥〷㙢〳ㄳ〳㥢㄰㤸㌱昴慡〶㜱〱㌳て㉥㤹㔶ㄲ㥤ㅡぢ㤷㈰㘰㤶㈴〲㘶戱愳昰㍤㥣ㅦ㡦㐸搹昸戳ㄶ㈱愹戵㤸㘴〹挹㌹㈴㑢㐱搴ㄹ〹㠱㔹㐶㥢攵㈴㉢㐰っ㘰捥户㔹㌵〱㠱㕢㌱昸〵㌴扡㄰㐴攵㠲戵㠱戹〸㙣㐲㘰㈶搲慢ㅡ挴〵捣㈵㜰挹戴㤲攸搴㈴戸〴〱㔳㥣〸㤸㈲㐷攱晢㐴㘱ち㈲㘵攳捦㕡㠵愴搶㙡㤲㙢㐸慥㈵戹づ㐴㑤㑦〸捣㕡摡慣㈳戹ㅥ挴〰收㐶㥢㔵㔳ㄱ戸ㄵ㠳摦㐴愳昵㈰敡〴戰㌶㌰ㅢ挰㈶〴㘶ㅡ扤慡㐱㕣挰摣ち㤷㑣㉢㠹㑥㥤〸㤷㈰㘰挶㈷〲㘶㥣愳昰㝤ち㜲㌲㈲㘵攳捦扡〷㐹慤㝢㐹敥㈳戹㥦攴〱㄰㌵㌲㈱㌰㥢㘸戳㤹攴㈱㄰〳㤸㐷㙣㔶㥤㠲挰慤ㄸ晣㔱ㅡ㍤〶愲昲挰摡挰㍣づ㌶㈱㌰愷搲慢ㅡ挴〵捣ㄶ戸㘴㕡㐹㜴敡㌴戸〴〱搳㌳ㄱ㌰㍤ㅣ㠵敦愳㥢改㠸㤴㡤㍦敢㜹㈴戵戶㤳扣㐰昲㈲挹㑢㈰慡㜳㐲㘰㕥愱捤づ㤲㥤㈰〶㌰慦搹慣捡㐷攰㔶っ晥㍡㡤摥〰㔱㔱戰㌶㌰㙦㠲㑤〸㑣〱扤慡㐱㕣挰扣〳㤷㑣㉢㠹㑥ㄵ挲㈵〸㤸㤶㠹㠰㘹攱㈸㝣ㅦ㌷ㄵ㈱㔲㌶晥慣㡦㤰搴摡㐳昲㌱挹㈷㈴㥦㠲愸愶〹㠱昹㥣㌶㝢㐹扥〰㌱㠰昹捡㘶ㄵ㍦扤㙡挵攰㕦搳攸ㅢ㄰㌵ぢ慣つ捣户㘰ㄳ〲㌳㤳㕥搵㈰㉥㘰扥㠷㑢愶㤵㐴愷㑡攰ㄲ〴㑣㝡㈲㘰搲ㅣ㠵敦㌳戲㌲㐴捡挶㥦昵〷㤲㕡㝦㤲晣㐵㤲㤲ち愲㐰搴㥦㝦㈴扡昲慤㐷㥢㌴㤲㜴㄰〳㤸晡㌶慢捡ㄱ戸ㄵ㠳㘷搰㠸㤳㠴搴ㅣ戰㌶㌰㤹㘰ㄳ〲㌳㥢㕥搵㈰㉥㘰ㅡ㌱慥㤵㐴愷㉡攰ㄲ〴捣ㄷ搸㠸挰㝢愵扤㡥挲昷挱㕥っ㤱戲昱㘷ㅤ挴摡㥢㤲㌴㈳㌹㤸攴㄰㄰戵㈷㈱㌰捤㘹搳㠲愴㈵㠸〱㑣戶捤慡㉡〴ㄶ㘰㕡搱愸㌵㠸㥡〷㤱つ㑣ㅢ戰〹㠱㤹换㤲慡㐱㕣挰ㅣ挱戸㔶ㄲ㥤㥡て㤷㈰㘰㜶㈶〲㘶㠷愳昰㝤ㅡ㜹㍡㈲㘵攳捦㍡㠶戵㜷㈶挹㈱改㐲搲ㄵ㐴㙤㑦〸㑣㜷摡昴㈰改〹㘲〰搳摢㘶搵ㄹ〸㉣挰昴愱搱戱㈰敡㑣㠸㙣㘰㡥〳㥢㄰㤸㠵㉣愹ㅡ挴〵㑣㝦挶戵㤲攸搴㔹㜰〹〲收愱㐴挰㙣㜶ㄴ扥㑦㔰ㄷ㈱㔲㌶晥慣ㄱ慣㝤㈴挹㈸㤲搱㈴㘳㐰搴扤〹㠱ㄹ㑢㥢㜱㈴攳㐱っ㘰㈶摡慣㕡㡣挰〲㑣㉥㡤㈶㠱愸㜳㈰戲㠱㤹っ㌶㈱㌰㑢㔸㔲㌵㠸ぢ㤸㘹㜰挹戴㤲攸搴㔲戸〴〱㜳㝤㈲㘰搶㌹ち摦挷扥换㄰㈹ㅢ㝦㔶〴㐹慤改㈴昹㈴〵㈴㔱㄰戵㍡㈱㌰㌳㘸㔳㐴㔲っ㘲〰㌳换㘶ㄵ㍦㐵ㄶ㘰㑡㘸㔴ち愲昸㌱戱つ㑣ㄹ搸㠴挰慣㘰㐹搵㈰㉥㘰收㌰慥㤵㐴愷捥㠷㑢㄰㌰㉢ㄲ〱戳摣㔱昸㍥慢扥㄰㤱戲昱㘷㥤捥摡捦㈰㔹㐸㜲㈶挹㔹㈰㙡㜱㐲㘰ㄶ搱㘶㌱挹ㄲ㄰〳㤸愵㌶慢㉥㐲㘰〱收㕣ㅡ㉤〳㔱晦㠲挸〶㘶㌹搸㠴挰㕣捣㤲慡㐱㕣挰㥣捦戸㔶ㄲ㥤扡〴㉥㐱挰㤴㈷〲愶捣㔱昸㍥㘰扦っ㤱戲昱㘷㕤捥摡慦㈰戹㤲攴㉡㤲慢㐱㔴㔱㐲㘰㔶搱㘶㌵挹㌵㈰〶㌰搷搹慣扡ㅣ㠱〵㤸㌵㌴㕡ぢ愲慥㠴挸〶㘶ㅤ搸㠴挰㕣挱㤲慡㐱㕣挰摣挸戸㔶ㄲ㥤扡ち㉥㐱挰㑣㐹〴捣㘴㐷攱㥢ㄴ戰ㄲ㤱戲昱㘷㙤㘴敤㜷㤰摣㐹㜲ㄷ挹扦㐱搴戸㠴挰摣㐳㥢㝢㐹敥〳㌱㠰㜹挰㘶搵㉡〴ㄶ㘰ㅥ愴搱㈶㄰㜵つ㐴㌶㌰㥢挱㈶〴㘶㌵㑢慡〶㜱〱昳〸攳㕡㐹㜴敡㕡戸〴〱搳㌷ㄱ㌰挷㌹ち摦㑣㠶㌵㠸㤴㡤㍦㙢㉢㙢㝦㥡攴ㄹ㤲㙤㈴捦㠲愸ㅥ〹㠱㜹㥥㌶摢㐹㕥〰㌱㠰㜹挹㘶搵㕡〴ㄶ㘰㕥愶搱㉢㈰敡㝡㠸㙣㘰㜶㠰㑤〸捣㍡㤶㔴つ攲〲收㌵挶戵㤲攸搴つ㜰〹〲愶㙤㈲㘰摡㌸ち摦散㡢㥢㄰㈹ㅢ㝦搶晢㐸㙡㝤㐰昲㈱挹㉥㤲摤㈰慡㐵㐲㘰㍥愲捤ㅥ㤲㡦㐱っ㘰㍥戵㔹戵ㅥ㠱〵㤸捦㘸昴㌹㠸攲㘴つㅢ㤸扤㘰ㄳ〲戳㠱㈵㔵㠳戸㠰昹㡡㜱慤㈴㍡㜵ぢ㕣㠲㠰㘹㤰〸㤸㑣㐷攱㥢㌱㜲ㅢ㈲㘵攳捦晡㠹戵晦㑣昲ぢ挹慦㈴扦㠱愸戴㠴挰晣㐱㥢㍦㐹晥〲㌱㠰㔱昵㠴㔵户㈳戰〰㤳ち㠱㔵て㐴摤〱㤱つ㑣ㅡ搸㠴挰㙣㘴㐹搵㈰㉥㘰敡挳㈵搳㑡愲㔳㜷挲㈵〸㤸敦㝥㑦㜰攵晢慤愳昰㑤㜳昹㌷㈲㘵攳捦ち㈳愹戵ㅦ挹晥㈴㑤㐸づ〰㔱㝢攱ㅡ晣㌰晣㈰摡㌴㈵㘹〶㘲〰㜳㠸捤慡扢ㄱ㔸㠰㌹㤴㐶捤㐱搴扤㄰戵挱ㅦ㉥㤹挱㈶〴收ㅥ㕡㔴㠳戸㠰挹㠶㑢愶㤵㐴愷敥㠳㑢㄰㌰㙦㈵〲收㑤㐷攱㥤㥢㤳晥㈰㈲㜹㍦㝦㤴㘹摥昱㔹ぢ挶㝣㠸挶㌰づㄵ㑥㉥㉢㡥㔵㌶㈸ㅣ㔸ㄵ㉢ㅦ㔶ㅣㅢ㔲ㄹ㙢㔸〸㠲愱戸ㅣ㈲ㅦ昰ㅢ㑥ㅤぢ愷ㄴ㐷攷㑤挲㈷㜰㠷昹㔵㤸〱㍦戸慡㌲㔶㉥ㅦ慤戶昴敢㠷㤴㡦㉤㡦つ㈹慥㥣㕤ㄲ㔹搰㌶㐰㙤㙢愶ㄶ㐵换㌰攳愴〲ㄳ㑦㙡㌲㉡㥦㍤㍢㕡㄰㔰㘳㙥㜹㔵㐵㝥㜴攴㤰㝦挲㥣ㄵ㘵㝦㐶㥣㠲㡦㈱㤵㑡㔱㠷㈷㥥愳㘱攰摥〲扤㐹挵㐷㤷敡㙦㑥㜹愸㠶㍦㈶戳㘳搷㑢㘱搲㑣扥㔲搲㌷㠱㑤扥㝢ㄸ㌳㘰ㅡ挰㌸戳㄰㉤戵㘵㡤㥣㈹㔶㈳换㉡㡢ぢ愲㤹づ㜷㝣㜱㔹㘳㘷㌸慥㉡收搲㐴收㌷㜱㌴昸㙣㜵㕣ㄹ摡㥥ㅦ愹㈸昸㈷㜴〴ㅢ㠶㤷摤づㄵ挲㝦㝦て㘴㍢㑣㑡捡㌷㝣ㅣ挱搷㌷㘷攳㝣㐲㥣㌷㠳〹晣㤸㍢㝥ㄸ㘲㘰㑣ㅥ捡㠲㝤㈳㐲ㅤㄷ㘷㤰㍢㍥ㅡ㈹㤳づ攴挶ち㠶㐴攷㌶ㄶ㡢㈸㜶㙣㉣㌸㈹㠹㌶㜱戳㌲摢挱㉡ㅣ㌸扤戲扣愴㉡ㄶ㙤ㅣㅦ挹〱㙥ㄵ㑥㡣㤶㐴㌸ㄱ慣㘱㝣㌴㍥㍦㠶愹㜲昱㜸㥣攴昵捦改づ㄰㐹㜳㍡愴愴㐷愱㈴㍢慥㝢㈳㜸散晣捤㡥愲㤱㠵昲晡慡扦㕡扤㡡慦㕢晢愷攸〱㝢㡢收㍥㠴昰戵㥦改挵愳愸㠹㥥㠰㘸㥦搹攴愴搵㔰换㌸挹慡㔱愱㥣敦㌰㤳㤲㙢㡤戲㜸搸㤴㘰㈱㔸慣㌸㍦㔲㔲戲愰㜱攱挸戲晣㤲慡㠲攸㤸挸昴㘸㠹㍥㔷㤷㔷㤴晥㐳晡㤵挶摤摦敥㔵ㄲ㕣㥣改㙦㈳戱㐰㑦捦㉢晢摢愷户ㄴ慢㈳捥㙣昲㔶㡢ㄸ㤹搶搱㝣㡢㐵㙢ㅥ㐶㈱晦攷㘹㜵㤹㜰摡㝦摦愴㔰㔹挲㠵搳㥡㑦挴昳ㄹ愷ㅤ挵㘷收挹ㄱ㘷㤸㡤㈹ㅦ㔳㡥㔹㤳〵㠶㘸㐴戱㉤晡挷ㅣ㔷搲愶㔰㈸昴㜷摦㔸㠰ㄵ㕥摦㌸㜳㈰㜰挲戳昹晥挴㥦ㅤ㜸ㄴ扣㜷挲㤲㜱〱㈲敦昹㜲ㄲっ挳㌰㡢㘷㌰晢㠲㘱㔲㜱慣㈴摡愰㔰昴㌲捥攰㈱㐱㌴敢ㄷ㑥㉡挲攴㥦㈱㡤ち㠷㔷ㄴㄷ㤴ㄴ㤷㐵㜹昱㠱㔹扣㕣㌶㌷㈶㍡〳昳㑤挷㤷㔷ㄶ㜳㌵㘸愳㐲㔹昶㌳㥢㜳扣昲ㄷ散敦攲愴㔹改㠵㠳㡡换㜰〰搹㌹㌹捥㉡捣㉤㉡㥦㠷〵愵㔵愵㘵挳㈳戳㉢晦ㄱ㡤㜲摥㑥㠰㤰㝤㔴愵慡搴㔴㤵㤱㥡昱㜷摦愷戰㠷㈳㘴ㄷ挴㑢㈵㜱㕡昵ㄸ㐶㐹㡥㔷㜶挹㤹敤换攳㤵㌵戹ㄶ㐷〶㑥㍦㡣慦挶攵㌹搸敡㠴挳戲攱㌱㈰愳㠶㑦ㅥ戹㙦㡥昸晦搷搲搶昴挷ㄱ㌹挹㕢㠱散ㄶ昱〹愹〷挲戸戱扤慢㔰挶㍤挷㤲㡥㤳昳敥㝥㤹㠵㘲挳㍤ㄱ敦㥥㌴攷㜰ㄸ愶て㌶挴㠱㡦㔳㉦愶㕤攲㥣摢搸㘶㜸ㄹ㔷ㅡ㈹愹㜴㜴㠳换㑢㑢㈳摣戵戸㕢收攲扣ㅤ捤㤰㙢㙡㥣㐹慣㐲㄰搹晦ㅣ㔱㘴㍥㐴㤱昹㈲挲摢㌱㈷㤹换㤸戱捡㘷㐴㉡㡡㘳㐵愵挵昹ㄹ㘴㌸ㄱ晣ㅦ戱㑦㘲ㄷ㑡〳㤸晡㈵㍢㈶㉥㔰扤㔳㍣敤㔹㠹㘸㜷㈷摣㌳㄰㍡戶ㅦ㝢㙥慡扣㠷慢扦㌹㠳ㄷ搷戰㜲戲户㜲㄰㉤ㅤ昷戳㄰㌸〷㠹㜱昱〵㠹㥣㠴搴ㄳ㌴挰㥦搵〵收晡㤵戶〵愳愴ㄳ㉤敢挳㈰㜳㑣㜹愴㘰ㄸ搶ち㤴㔷搴㜷㤶㘲㘷愰戵㍣愵㔴㠴㌹戹㜶㌰㘶愱㘳㜶晢㕣㕣〳㔷㘴㔰㤰㡢㘹慢㘹㥣㤶ㅢ戲㝢挸㠳㌶㈵㍤扤㐱㐶㔰慥㤱㍡㔶㕢㘷ㄲ愲戹㤴㝤愴㉦晥ㄷㄳ㝡攱捣捡捤攲㘵㠴搵ㄵ㥢㘳㜵〳㔱㑦㠲攵昶㜸っ扡搳愰〷㐸晡㔶㈸扤㐷㐹挲㠹愸㜰㐸㐹㉦攵〴搹㡣㔲㙥づ㉥㌷㐲㤸㌶㡢㠹戶㠰㈴搴㈰攳㈹攸慤㥥戰㝡㘱晢昶扥ㄸ愷愸㙤㈰㍡㍦㡦㌱愷挰㕥捣摦ㅢ㐴扤〲㈱㙦㐶愵㙤昸㤸㠴㈹昶摤㠸愸ㅤ㘰㜹㌳愲㕦㐶ㄷ㥤ㅥ敥㠴㡡㤷搱㙣㘴㑤㤷㘴敡㔵搸昱戲っ㜳㤶㔸㐱㌵㐶㜲㕤搰てㅣ摥㤵搴㙢㄰昰摡挰㝥㈵㝣昷㔲㙦挰㠰敦㘰㈹㠱㘷㑣昵㈶㌴㍣㙢㕡晤戹㠹㙦㘱挴㤳㔱㝣攷ㅣ〸㘹捤㍢攷㍢昴挰㥦㌵〸收晡愵摥挵㐸〳㑡愱〳攸㘰搸㔸㐳㤸敤扤㘰㠳愱㌴ㄸ㐶㠳昷㘱挰慥㕢挳挱挵ㅢ戵换㜰㍢〰㘳㈷敥〸扡㡤愴摢攷㄰ㅡ㡤ㅡつ㤹搹愸扤㘰㤳㌷敡ぢ㔸搴扡㔱㕦挲搸㙥搴ㄸ㔶㔰つ㔶ㅡ㌵ㄶㅣㅢ昵ㄵ〴戵㘹搴㌷戰㑢搲愸㙦愱㤶㐶㡤攳㈶㝥〷捥搵愸〹㤰搶摣愸敦攱收㍢㡢愸ㅦ㈰つ㘸㔴㉥㌷㘷ㄲ戳晤ㄸ㙣㌰㤹〶㔳㘸昰ㄳっ愴㔱㔳挱挵ㅢ昵慢攱㘶㌴㙡ㅡ摤㑥愰㕢㍤搴㘲㌴敡㈴挸捣㐶昱㈲㍣㜹愳搲㘱㔱敢㐶㠵㘰㙣㌷敡㘴㔶㔰㉤挹㜰愵㝤㉡㌸㌶慡㍥昴戵㘹ㄴ愷㥥㈶㘹ㄴ㈷愵㑡愳昲戸㠹つ挰戹ㅡㄵ㠱戴收㐶㜱ㄶ㉢晥戹㑦昷慡㌱㐴〱㡤捡攷收ㄴ㌰㕢㔶戰㐱㤴〶㠵㌴攰挴㔷㘹搴っ㜰昱㐶㜱㙥慢㡥㙢㌴慡㠸㙥挵㜴攳㍣㔴愳㔱戳㈰㌳ㅢ搵〲敡攴㡤攲昴搵㕡㌷敡㌰ㄸ摢㡤㉡㘱〵昱㐶㤵㠱㘳愳戲愱慦㑤愳㌸ㄵ㌶㐹愳摡㐰㉤㡤㉡攷㈶戶〵攷㙡搴ㅣ㐸㙢㙥搴ㄱ㜰挳㍦㑦愳㡥㠴㐸〳ち愵㍥㐵㔵㜲㜳昸慤㉥㡡搳㙥〳っ慡㘸㌰㤷〶㥣㠸㉢㡤㥡〷㉥摥㈸捥戵搵㙥㐶愳收搳㙤〱摤㌸㉦搶㘸搴ㄹ㤰㤹㡤攲㡣搹攴㡤攲㜴摡㕡㌷㡡搳㙥敤㐶㉤㘴〵搵㤲っ㐷搴㔹攰搸㈸捥挸慤㑤愳㌸㌵㌷㐹愳㌸㘹㔷ㅡ㜵㌶㌷戱㉦㌸㔷愳ㄶ㐳㕡㜳愳晡挳つ晦㍣㡤ㅡ〰㤱〶ㄴ㑡摤愸㜳戸㌹㑢㤹㙤㘰戰挱戹㌴㔸㐶〳㑥っ㤶㐶㉤〷ㄷ㙦搴㔰挳捤㘸搴ち扡㥤㐷户戱㌰㌰ㅡ㜵〱㘴㘶愳挶㐱㥤扣㔱㥣摥㕢敢㐶㜱ㅡ戰摤愸ぢ㔹㐱戵㈴㐳愳㉥〶挷㐶㜱㠶㜰㙤ㅡ㌵〹㜶㐹ㅡ挵㐹挴搲愸㝦㜱ㄳ㌹㥢搸搵愸㑢㈱慤戹㔱㥣㜵㡣㝦㥥㐶㜱敡㜱㐰愳㉥攷收㕣挱㙣㥣㤶ㅣ㘰㜰㈵つ慥愲〱㈷㉡㑢愳慥〶ㄷ㙦ㄴ攷㈲㙢㌷愳㔱㉢改戶㡡㙥㌳㘰㘰㌴敡ㅡ挸捣㐶㜱㐶㜱昲㐶㜱扡㜱慤ㅢ挵㘹挹㜶愳慥㘵〵昱㐶慤〱挷㐶捤㠲扥㌶㡤攲搴攵㈴㡤㉡㠳㕡ㅡ戵㤶㥢㔸づ捥搵愸敢㈱慤戹㔱㥣〵㡤㝦㥥慢㍥㑥㠵搶㠰㐲愹㡦愸ㅢ戹㌹㌷㌱ㅢ愷㐹〷ㄸ慣愷挱〶ㅡ昰扥㕣ㅡ㜵㌳戸㜸愳㌸㌷㕡扢ㄹ㡤扡㠵㙥户搲㙤ㄱっ㡣㐶摤づ㤹搹愸挵㔰㈷㙦ㄴ愷㍦搷扡㔱㥣㈶㙤㌷㙡㈳㉢愸㤶㘴㌸愲敥〴挷㐶㉤㠵扥㌶㡤㕡〶扢㈴㡤㕡づ戵㌴敡㉥㙥㈲㘷㕢扢ㅡ㜵㌷愴㌵㌷㡡戳戲昱捦㜳㐴㕤〰㤱〶ㄴ㑡摤愸㝢戹㌹昷㌱ㅢ愷㙤〷ㄸ摣㑦㠳〷㘸挰㠹摣搲愸〷挱挵ㅢ挵戹摡摡敤愰㝤㜱㌷搱㙤㌳摤㌸慦摡㘸搴挳㤰㤹㡤攲㡣敢攴㡤攲㜴散㕡㌷㡡搳戶敤㐶㍤挲ち慡㈵ㄹㅡ昵ㄸ㌸㌶敡㍡攸㙢搳愸戵戰㑢搲愸㜵㔰㑢愳ㅥ攷㈶㕥て捥搵愸㈷㈰慤戹㔱㥣㈵㡥㝦㥥㐶摤〴㤱〶ㄴ㑡摤愸㈷戹㌹㑦㌱摢晡㘰㠳慤㌴㜸㥡〶ㅢ㘰㈰㡤㝡〶㕣扣㔱㥣㍢慥攳ㅡ㐷搴㌶扡㍤㑢㌷捥昳㌶ㅡ昵㍣㘴㘶愳㌸〳㍣㜹愳敥㠳㐵慤ㅢ挵㘹攴㜶愳戶戳㠲㙡㐹㠶㐶扤〸㡥㡤攲っ昳摡㌴㡡㔳捤㤳㌴㡡㤳搰愵㔱㉦㜱ㄳ㌹ㅢ摤搵愸㔷㈰慤戹㔱㥣戵㡥㝦㥥㐶㍤ち㤱〶ㄴ㑡摤愸㥤摣㥣㔷㤹㡤搳摡〳っ㕥愳挱敢㌴㜸ㅣ〶搲愸㌷挰挵ㅢ挵戹散摡捤㘸搴㥢㜴㝢㡢㙥捦挳挰㘸搴㍢㤰㤹㡤攲㡣昴攴㡤攲㜴昵㕡㌷敡㐵ㄸ摢㡤㝡㤷ㄵ㔴㑢㌲㌴敡㝤㜰㙣搴㑢搰搷愶㔱㥣晡㥥愴㔱㥣ㄴ㉦㡤晡㠰㥢挸搹昱慥㐶敤㠲戴收㐶㜱ㄶ㍤晥㜹ㅡ挵愹昴ㅡ㔰㈸㜵愳晥挳捤昹㠸搹㌸捤㍥挰㘰てつ㍥愶〱㈷摥㑢愳㍥〱ㄷ㙦ㄴ攷搶㙢㌷攳ㄱ搲愷㜴晢㡣㙥ㅦ挱挰㘸搴㕥挸捣㐶敤㠱㍡㜹愳㍥㠶㐵慤ㅢ昵〹㡣敤㐶㝤挱ち慡㈵ㄹㅡ昵ㄵ㌸㌶㡡㌳昰㙢搳㈸㑥挵㑦搲愸扤㔰㑢愳扥收㈶㜲戶扥慢㔱摦㐲㕡㜳愳扥㠲ㅢ晥㜹ㅡ昵㌵㐴ㅡ㔰㈸㜵愳晥换捤昹㥥搹㌸敤㍦挰攰〷ㅡ晣㐸〳㉥〴㤰㐶晤〴㉥摥愸敦つ㌷攳㠸晡㤹㙥扦搰敤てㄸㄸ㡤晡つ㌲戳㔱㥣戱㥦扣㔱㝦挱愲搶㡤㑡㐹搵㡤晡㥤ㄵ㔴㑢㌲㌴敡㑦㜰㙣㤴㠲扥㌶㡤攲搲㠰㈴㡤㑡㠳㕡ㅡ昵ㄷ㌷㤱㍤㜱㌵㡡て挳㙢㙥ㄴ㔷ㄹ㘰摢㍣㔷㝤ㄹ㤰㙥㠱搴昳昰戶ㅥ㐲㕡昸扡挸ㄴ㘵〵ㅢ愴搳㈰㐴〳㉥㑣㤰㐶搵〷ㄷ㙦㔴㈳挳捤㘸㔴〶摤昸ㅤ愷㡡敢〴㡣㐶㌵㠰捣㙣㔴㔳愸㤳㌷㡡换ぢ㙡摤愸㠳㘱㙣ㅦ㔱つ㔹㐱戵㈴㐳愳ㅡ㠳㘳愳づ㠱扥㌶㡤攲㔲㠵㈴㡤攲㈲〶㘹㔴ㄶ㌷戱㈵㌸㔷愳昶㠳戴收㐶㘵挳㑤ㅡ㘵㝥㘲愰㕡㐱扡挵摦愸㈶摣㥣〳㤸慤㜵戰挱㠱㌴㌸㠸〶㕣㈸㈱㡤㙡ち㉥摥愸㈳っ㌷攳搴搷㡣㙥〷搳㡤敢ㄶ㡣㐶ㅤち㤹搹㈸慥㘸㐸摥㈸㉥㜷愸㜵愳戸㉣挲㙥㔴㜳㔶㄰㙦㔴㑢㜰㙣ㄴ㔷㑣搴愶㔱㕣㍡㤱愴㔱㕣㔴㈱㡤㍡㡣㥢搸ㄳ㥣慢㔱慤㈰慤戹㔱扤攱收㙦㔴ㅦ㐸户昸ㅢ搵㠶㥢搳㤶搹戸㑣㈳挰攰㜰ㅡㅣ㐱〳㉥摣㤰㐶ㅤ〹㉥摥㈸慥捤搰㙥挶ㄱ搵㡥㙥敤改㌶〲〶㐶愳㍡㐲㘶㌶㙡㈴搴挹ㅢ挵攵ㄷ戵㙥ㄴ㤷㘹搸㡤㍡㡡ㄵ挴ㅢ搵〹ㅣㅢ挵ㄵㅣ戵㘹ㄴ㤷㜲㈴㘹ㄴㄷ㜹㐸愳㡥攱㈶㜲戵㠷慢㔱㌹㤰搶摣㈸慥ち昱㥦晡戸㌴㘴㡢扦㔱㕤戹㌹摤㤸㡤换㐶〲っ扡搳愰〷つ戸㤰㐴ㅡ搵ㄳ㕣扣㔱㕣㉢愲摤㡣㐶昵愲㕢㙦扡㐵㘰㘰㌴敡㔸挸捣㐶㑤㠷㍡㜹愳戸ㅣ愴搶㡤㉡㠰戱摤愸攳㔸㐱扣㔱晤挰戱㔱㔱攸㙢搳㈸㉥㉤㐹搲愸㈲愸愵㔱晤戹㠹挵攰㕣㡤ㅡ〸㘹捤㡤攲㉡ㄵ晦ㄱ挵愵㉡㕢晣㡤ㅡ捣捤ㄹ挲㙣㕣挶ㄲ㘰㌰㤴〶挳㘸挰㠵㉤搲愸攱攰攲㡤攲摡ㄵ敤㘶㌴㙡〴摤㐶搲敤㜴ㄸㄸ㡤ㅡつ㤹搹㈸慥㐰㐹摥㈸㉥㑦愹㜵愳戸㡣挵㙥搴ㄸ㔶㄰㙦搴㔸㜰㙣搴㔹搰搷愶㔱㡢㘰㤷愴㔱㡢愱㤶㐶㡤攳㈶㉥〱攷㙡搴〴㐸㙢㙥搴㔲戸昹ㅢ㜵㉥愴㕢晣㡤捡攵收㑣㘲戶㘵挱〶㤳㘹㌰㠵〶㕣㘸㈳㡤㥡ち㉥摥㈸慥愵搱㜱㡤昷愸㘹㜴㍢㠱㙥㕣昷㘲㌴敡㈴挸捣㐶㜱㐵㑣昲㐶㜱戹㑣慤ㅢ挵㘵㌵㜶愳㑥㘶〵昱㐶㥤ち㡥㡤扡ㅡ晡摡㌴㙡ㄵ散㤲㌴㙡㌵搴搲愸㍣㙥㈲㔷攷戸ㅡㄵ㠱戴收㐶㜱ㄵ㡦扦㔱㙢㈰摤攲㙦㔴㍥㌷愷㠰搹戸捣㈷挰㈰㑡㠳㐲ㅡ慣㠳㠱㌴㙡〶戸㜸愳戸戶㐷扢ㄹ㐷㔴ㄱ摤㡡改挶㜵㌸㐶愳㘶㐱㘶㌶㡡㉢㜴㤲㌷㡡换㜷㙡摤㈸㉥昳戱ㅢ㔵挲ち攲㡤㉡〳挷㐶㜱〵㔰㙤ㅡ挵愵㐰㐹ㅡ挵㐵㐲搲愸㜲㙥㈲㔷ぢ戹ㅡ㌵〷搲㥡ㅢ挵㔵㐵晥㐶㍤〸改ㄶ㝦愳㉡戹㌹㌱㘶攳戲愳〰㠳㉡ㅡ捣愵挱㘶ㄸ㐸愳收㠱㡢㌷㡡㙢㡤戴㥢㜱㐴捤愷摢〲扡㙤㠵㠱搱愸㌳㈰㌳ㅢ昵㌴搴挹ㅢ挵攵㐴戵㙥搴㌶ㄸ摢㡤㕡挸ち攲㡤㍡ぢㅣㅢ昵㉣昴戵㘹ㄴ㤷㈶㈵㘹ㄴㄷ㉤㐹愳捥收㈶㜲昵㤲慢㔱㡢㈱慤戹㔱㕣攵攴㙦ㄴ㤷㍡㙤昱㌷敡ㅣ㙥捥㔲㘶攳㌲愸〰㠳㜳㘹戰㡣〶㕣ㄸ㈵㡤㕡づ㉥摥㈸慥㝤搲㙥挶ㄱ戵㠲㙥攷搱敤㝤ㄸㄸ㡤扡〰㌲戳㔱㕣挱㤴扣㔱ㅦ挲愲搶㡤摡〵㘳扢㔱ㄷ戲㠲㜸愳㉥〶挷㐶敤㠶扥㌶㡤攲㔲愹㈴㡤摡〳戵㌴敡㕦摣挴㡦挱戹ㅡ㜵㈹愴㌵㌷敡㔳戸昹ㅢ昵ㄹ愴㕢晣㡤扡㥣㥢㜳〵戳㜱㔹㔶㠰挱㤵㌴戸㡡〶㕣愸㈵㡤扡ㅡ㕣扣㔱㕣㡢愵摤㡣㐶慤愴摢㉡扡晤〴〳愳㔱搷㐰㘶㌶㡡㉢慡㤲㌷敡ㄷ㔸搴扡㔱扦挲搸㙥搴戵慣㈰摥愸㌵攰搸㈸慥搸慡㑤愳戸㜴㉢㐹愳晥㠴㕡ㅡ戵㤶㥢挸搵㕤慥㐶㕤て㘹捤㡤㔲㝣慡〱㌴摣戳㤰戸ㄴ㙣㡢扦㔱㌷㜲㜳㙥㘲戶㝡挱〶敢㘹戰㠱〶㘹㌰㤰㐶摤っ㉥摥愸晡㠶㥢㜱敡扢㠵㙥户搲㡤敢戸㡣㐶摤づ㤹搹愸晤愰㑥摥㈸㉥晦慡㜵愳㥡挰搸㙥搴㐶㔶㄰㙦搴㥤攰搸愸〳愰慦㑤愳づ㠲㕤㤲㐶㌵㠵㕡ㅡ㜵ㄷ㌷戱ㄹ㌸㔷愳敥㠶戴收㐶㜱㔵㥡晦㠸㍡ㄴ搲㠰㐶摤换捤戹㡦搹㥡〷ㅢ摣㑦㠳〷㘸挰㠵㙣搲愸〷挱挵ㅢ挵戵㙡㍡慥㜱㐴㙤愲摢㘶㤰㜴慥㈸慡摤ち㈶捥愶っㅢ换捡㌸昷戶㜲扦挲〹㔵㤱ㄲ晣㕡捡㌸慣㜱㠸㔱昴㑦㤸摣㥡㘶慦㌴昱㝥晢戴晢㐷㔴戰㌸㑢㌶攱愴㔳㕡㘲换扣ㄸ戸㙤㥤㙤慢愴攵摦㕢㠹㤲㤹㍥散户扦晥慡㕤ㄶ敥ㅥ昵攷昲换㑥昳昲㔲㌲㤸ㄳ㑤挲㤲挳㠷搱㌰散捥改ㅤ挱㈶㤹攸敤㔹㤸挱㘸㑤昶㑤㑢攵〴攴㡥㈵晣㝤愵愰昹慣敥昹摥㡦㈰愱攲㕡っ搹㘱ㅦ〵愷㕦慡㤳㤶㍥㐶ㅢ㠸㔹㘲㝡づ㘸㡤㌳㠸ㄹ〶换捤㌰㤷㌸㌷戶愰〴昳户㌹攴㤷㝥摡㈳㑥㔸戵搵㈸扡扣㈲つ换敤扣㕦改ㅢ昷㝤〰愱ㅡㅣ攰昹ち㘵㜱愳收ㄸ㔴㤳㍥㄰戰㈷昴㜷㈳㑤ㅦ扥㐲搵㈸昱㠰攳㡢昳㉢捡㉢换ぢ㘳搹戹昸㔵㥣㙣㝥愹㌶扥ㅣ愸昳挰昴晥㠸ㄸ㤸㤳ㅢ㤶㔶挶ㅦぢ㤲收㘵捥㉡㉢㥦㔷㈶搵愴㔷昲扢挵〵挵晡昵㤹㠶㙢㔴攴搵〶攰㠵昵㐳捡㜰㔷愲㠸㔷戸㥢ㅥ㜴搷㠳ㅥ捥㈰慢㈷〶㜴て㠹攵晦㤰㠴㝢㈱㌲戳㠴戶㘰㑢昶ㅢ㍣㈸捦晤㠳㐸愱㈷㈱㙥〸戱捣㡢㥥㠸敦攳づ㍤〵㐹㘳㐸㡣戵〵攱摥㑥ㄴ㙢㉢㤴㔶㉢挴戳戲㐱搴戱㤰昳㙣㤳愹㝡〱㐰ㅥつ捣㤵㘹㍤ぢ㌳㥥愴㡦〳换㍤摢㝡づ〲搵て㈳挱换戵搷昵搷搲敤戴㠱㍢㜸㑣㔳〲攵㥥愷扡㈲㈸晢つ㘱㑡攸㐵㤸㈴㙣愲捡㠱ㄹㅢ改㙥㠴㥥挲ㅢㅥ捣挰㜸㠵㠷攸挱㔰㍤ㄸ收っ戲㠶㘳㔰㌷㡤ㄸ㠱挸捣ㄲ㝡ㄹ摢㄰搰㠸㔷㈰㜶㌷㘲〷㈴摥㐶㡣㜴愲㔸㍢愱㤴㥦㑦戲㡥㐰㔰㌵ㅡ㜲扢ㄱㅤ〰挰扥㐶扣〱㌳㌶㘲っ昴搲㠸㌷㈱㔰㘳挱昹ㅢ㌱㑥㑢摦愶つ愲㠲㑦㔱ㄳ㐰愵ㄱ㠷㈳戰㙥㠴挵愳㠹〷㡥㙡ㄳ㠸㜹㉥㕤昱ち㑦搲㠳挹㝡㌰挵ㄹ㘴㑤挵愰㙥愰㥥㠶挸捣㘲㜱㥦户戸㠷㕢摣愹挳㈷㘸昹㉥㡡㡥愶挵㔱㈰敡㈴挸㙤昰㥡扢挰摢〳㌳㠲㜷㌲昴〲摥挷㄰愸㔳挱昹挱换搳搲㑦㘹㠳愸攰昱㐴ㄳ㔴挰㙢ㅡ〸摥㠱㠱攰攵搳ㄵ慦㜰㠱ㅥ㐴昵愰搰ㄹ㘴捤挰愰㙥挰㉢㐲㘴㘶昱㠲㔷慣攵㕦ㄳ扣慥戴攰㍡㈵㌵ぢ㜲ㅢ扣挶㉥昰晥敢㠰㔷〲扤㠰昷㍤㠱㈹〳攷〷慦㕣㑢㝦㌴挱㥢〳愹㠰㘷〵㠲㔷㍦㄰扣㑡㌸昱ㄵ㡥改㐱㤵ㅥ捣㜵〶㔹昳㌰愸ㅢ昰收㈳㌲戳㜸挱㕢愰攵㝦㄰扣摥戴攸〵愲捥㠰摣〶㉦挵〵ㅥ㝦挲㡣㝢摥㐲攸〵扣㔴〸搴㔹攰晣攰㥤慤愵㘹戴㐱㔴昰昸挶ㅦ㔰〱敦户㕦㠳づ摢㕦㈰昵㥦㉡捦愱㉢㕥攱愵㝡㜰慥ㅥ㉣㜳〶㔹换㌱愸ㅢ昰㔶㈰㌲戳㜸挱㍢㑦换ㅢ㘰〳攵㈷捡慣㝥㌰㔳ㄷ㐰㙥㠳昷ㅤ戶㘶摦㌹㉦换〱敦㐲攸〵扣㌰㠱戹ㄸ㥣ㅦ扣㝦㘹改晥㈶㜸㤷㐲㉡攰㝤ㄹ〸摥摥㐰昰㉥㠷ㄳ㕦攱㉢昴攰㑡㍤戸捡ㄹ㘴㕤㡤㐱摤㠰户ㄲ㤱㤹挵ぢ摥㉡㉤㍦㤸攰つ愵挵㄰㄰㜵つ攴㌶㜸ㅦ戹挰㙢〱㌳敥㜹搷㐲㉦攰戵㈴㌰㙢挰昹挱㕢慢愵搹戴㐱㔴昰㤸㉡〶㉡攰㝤㘰㠲挷㜷㙥㜹挳㜸㉦㄰扣ㅢ改㡡㔷昸㈶㍤㔸慦〷ㅢ㥣㐱搶捤ㄸ搴つ㜸户㈰㌲戳㔸㝣㙦戶昸㑥㙣昱捤㌷㝣慢㤶ㅦ㠹つ㤴摦㤴戳㐶挱㑣摤づ戹つ摥敢㉥昰㍡㍡攰㙤㠴㕥挰㍢㡡挰摣〹捥て摥㕤㕡摡挹〴敦㙥㐸〵扣㔷㑣昰攲敦戶㉦〵㠲㜷㉦㥣昸ち摦愷〷昷敢挱〳捥㈰敢㐱っ敡〶扣㑤㠸捣㉣摥㍤㙦戳㤶㜷㈷㜸ㄳ㘸㌱ㅥ㐴㍤っ戹つ摥㌶ㄷ㜸扤ㅤ昰ㅥ㠱㕥挰敢㐳㘰ㅥ〳攷〷敦㜱㉤㍤捥〴敦〹㐸〵扣㈷〳挱㝢㈲㄰扣㈷攱挴㔷昸㈹㍤搸慡〷㑦㍢㠳慣㘷㌰愸ㅢ昰戶㈱㌲戳㜸挱㝢㔶换〷ㄳ扣愹戴㤸〲愲㥥㠷摣〶敦㈱ㄷ㜸挳ㅤ昰戶㐳㉦攰㡤㈰㌰㉦㠲昳㠳昷㤲㤶㡥㌲挱㝢〵㔲〱敦晥㐰昰敥つ〴㙦㈷㥣昸ち扦慡〷慦改挱敢捥㈰敢つっ敡〶扣㌷ㄱ㤹㔹扣攰扤愵攵ㄳ〸摥㈹戴㌸ㄹ㐴扤〳戹つ摥㐶ㄷ㜸㤳ㅤ昰摥㠵㕥挰㥢㐲㘰摥〷攷〷敦〳㉤㥤㘶㠲户ぢ㔲〱敦收㐰昰搶〷㠲昷ㅦ㌸昱ㄵ晥㐸て昶攸挱挷捥㈰敢ㄳっ敡〶扣㑦ㄱ㤹㔹扣攰㝤愶攵㜹〴㉦㥦ㄶ搳㐱搴㕥挸㙤昰搶戸挰换㜷挰晢〲㝡〱慦㠰挰㝣〵捥て摥搷㕡㕡㘸㠲昷㉤愴〲摥慡㐰昰慥づ〴敦扦㜰攲㉢晣扤ㅥ晣愰〷㍦㍡㠳慣㥦㌰愸ㅢ昰㝥㐶㘴㘶昱㠲昷㡢㤶㤷ㄲ㍣㝥愱慦㔵〴愲㝥㠳摣〶敦ㄲㄷ㜸㜳ㅣ昰㝥㠷㕥挰慢㈰㌰㝦㠲昳㠳昷㤷㤶挶㑣昰ㄴ摥愷〴扣ぢ㑣昰攲敦戶攷〵㠲㔷て㑥㝣㠵搳昴㈰㕤て㐲捥㈰慢㍥〶㜵〳㕥〶㈲㘳㕢㝣敦戶㤶㤶㥦㐱昰捡㘹㔱〶愲ㅡ㐰㙥㠳户挴〵摥搹づ㜸つ愱ㄷ昰ㄶㄱ㤸挶攰晣攰㘵㘹改ㄲㄳ扣晤㈰ㄵ昰捥㌴挱㡢扦摢㥥ㄱ〸㕥ㄳ㌸昱ㄵ㍥㐰てづ搴㠳㠳㥣㐱㔶㔳っ敡〶扣㘶㠸㉣攰㜹敥㙤て搶昲昳〸㕥ㄵ敡戳㘲㈰敡㔰挸㙤昰㘲㉥昰㉥㜲挰㙢づ扤㠰㜷㌱㠱㘹〹捥て摥㘱㕡㝡㠹〹㕥㉢㐸〵扣昲㐰昰㑡〳挱㙢〳㈷扥挲㙤昵攰㜰㍤㌸挲ㄹ㘴ㅤ㠹㐱摤㠰搷づ㤱㠳挰㙢慦攵㔷ㄳ扣㌳㔰㥦㜵㍡㠸敡〸戹つ㕥愱ぢ扣㙢ㅣ昰㡥㠲㕥挰扢㤶挰㜴〲攷〷敦ㄸ㉤㕤㘳㠲㤷〳愹㠰ㄷ㌱挱㡢ㅦ戶㜹㠱攰㜵㠵ㄳ㕦攱㙥㝡搰㕤て㝡㌸㠳慣㥥ㄸ搴つ㜸扤㄰㌹攸戰敤慤攵敢〹摥㘲搴㘷㉤〲㔱挷㐲㙥㠳㌷捤〵摥慤づ㜸挷㐱㉦攰摤㐶㘰晡㠱昳㠳搷㕦㑢㌷㥡攰つ㠴㔴挰换㌵挱㡢ㅦ戶ㄳ〲挱ㅢっ㈷扥挲㐳昴㘰愸ㅥっ㜳〶㔹挳㌱愸ㅢ昰㐶㈰㜲搰㥥㌷㔲换敦㈵㜸换㔱㥦戵っ㐴㡤㠶摣〶㙦㤴ぢ扣〷ㅤ昰挶㐰㉦攰㙤㈲㌰㘳挱昹挱ㅢ愷愵て㤹攰㑤㠰㔴挰ㅢㅡ〸摥攰㐰昰㜲攱挴㔷㜸㤲ㅥ㑣搶㠳㈹捥㈰㙢㉡〶㜵〳摥㌴㐴づ〲敦〴㉤㝦㠲攰㕤㠴晡慣ぢ㐱搴㐹㤰摢攰ㅤ攷〲㙦慢〳摥挹搰ぢ㜸㑦ㄳ㤸㔳挱昹挱换搳搲㙤㈶㜸ㄱ㐸〵扣㥥㠱攰㜵て〴㉦ㅦ㑥㝣㠵ぢ昴㈰慡〷㠵捥㈰㙢〶〶㜵〳㕥ㄱ㈲〷㠱㔷慣攵㉦ㄱ㍣㝥㤹戱㜵ㄹ㠸㥡〵戹つ㕥㈷ㄷ㜸㍢ㅤ昰㑡愰ㄷ昰㕥㈵㌰㘵攰晣攰㤵㙢改敢㈶㜸㜳㈰ㄵ昰摡〷㠲㜷㘴㈰㜸㤵㜰攲㉢ㅣ搳㠳㉡㍤㤸敢っ戲收㘱㔰㌷攰捤㐷攴㈰昰ㄶ㘸昹㝢〴㙦ㄵ敡戳㔶㠲愸㌳㈰户挱换㜶㠱户换〱㙦㈱昴〲摥㙥〲㜳ㄶ㌸㍦㜸㘷㙢改㐷㈶㜸㡢㈱ㄵ昰づつ〴敦攰㐰昰捥㠱ㄳ㕦攱愵㝡㜰慥ㅥ㉣㜳〶㔹换㌱愸ㅢ昰㔶㈰㜲㄰㜸攷㘹昹㕥㠲户ㄶ昵㔹㙢㐰搴〵㤰摢攰敤敦〲敦㙢〷扣ぢ愱ㄷ昰扥㈱㌰ㄷ㠳昳㠳昷㉦㉤晤捥〴敦㔲㐸〵扣㐶㠱攰㌵〸〴敦㜲㌸昱ㄵ扥㐲て慥搴㠳慢㥣㐱搶搵ㄸ搴つ㜸㉢ㄱ㌹〸扣㔵㕡晥ぢ挱㕢㡦晡慣㥢㐰搴㌵㤰摢攰愵戹挰晢〳㘶昲㍣て㝡〱敦㑦〲戳〶㥣ㅦ扣戵㕡捡捦㈱愹㘶〱敡㝡㐸〵扣扦㝥㌱㥥㈴挷㉦㔵晥㠰搴晦㈴昹㐶㌸昱ㄵ扥㐹て搶敢挱〶㘷㤰㜵㌳〶㜵〳摥㉤㠸㉣攰㜹㥦攷㘹㜹㝤㙣愰晣扡户㜵ㅢ㡡㔴户㐳㙥㠳昷㈳戶㘶摦㤳攴〶㌰㈳㜸ㅢ愱ㄷ昰ㅡㄲ㤸㍢挱昹挱扢㑢㑢ㅢ㥢攰摤つ愹㠰昷慤〹㕥晣㔲攵敢㐰昰敥㠵ㄳ㕦攱晢昴攰㝥㍤㜸挰ㄹ㘴㍤㠸㐱摤㠰户〹㤱㠳昶扣捤㕡㝥㈰挱攳ㄷ㌰㕢晣㡡㘷昵㌰攴〲㐷㌳挸改㈸㝢捤㈳㕡慡㍦〷㠷㈲㈵慣㍦昸つ㍦〶㌵晥攱㈷㔰攰搴愸㥥摡ち愶㉤昹敤㈴㉦㤰扣〸愲㜶〳愰㜷昰㑤捤扥㕦敤摣攵㈸㝣扦摡昹㉣㈲㐹㌹搹㘶㌹昲昹㌳愳敡㑦㠳㌱㑥〹㙦㠷㉤晥攱愷㔳散㉡㜶㠲㘹㑢摥㔳挵摢㠹慡㜸换㔱昸㝥㈲昳つ㐴㤲㉡摡㤹㔵扣愹愵㉥㔰昸㜱㉢晥攱㥢㠰敤㉡㜶㠱㘹ㅢ㔰挵㡥㐴㔵扣攲㈸㝣扦㐷戹〷㤱愴㡡捥㘶ㄵㅦ㙢愹慢㡡㑦㈱挵㍦㝣慡㘷㔷昱㌵㤸戶〱㔵㍣㤷愸㡡㘷ㅤ㠵敦挷ㅦ晦㡢㐸㔲㐵㉦戳㡡敦戵搴㔵挵㡦㤰攲㕦㡡搵挷慥㠲㥦㤷戵つ愸㘲㑢愲㉡㥥㜰ㄴ扥㕦㕡攴㐷㙡㔲挵〰戳ち昹㕣㑤戶㥡㝢慤昳ち昳㤳㌴愹㘲㤰㕤〵㍦㜸ち慡攲愱㐴㔵㙣㜶ㄴ扥㥦㌵攴㘷㔳㔲挵〸戳ち昹㠰ち挹㕤摦㠵ㄷ收㐷㔲㔲挵㈸扢ち㝥㠲ㄳ㔴挵㍤㠹慡戸摢㔱昸㝥㐳㤰ㅦ昲㐸ㄵ攳捤㉡攴㤳ㅥ㔶攱㍡㐶昸搹㡥㔴㌱搱慥㠲ㅦ㠵〴㔵㜱㕢愲㉡㙥㜵ㄴ扥ㅦ散攳愷㈵㔲挵㌴戳ち昹挸挴㠷〵㍦㈴㤱㉡㑥戴慢攰㘷ち㐱㔵摣㤰愸㡡敢ㅤ㠵敦搷昱昸戱㠳㔴㜱㥡㔹㠵㝣昶攰慢㠲㥦㌶㐸ㄵ搳敤㉡昸㜰㍥愸㡡搵㠹慡㔸攵㈸㝣㍦㐵挷攷昷㔲㐵㤱㔹㠵㍣挴昷㔵挱挷昶㔲挵㑣扢ち㍥攵づ慡攲戲㐴㔵㕣敡㈸㝣扦晢挶〷攱㔲挵㙣戳ち㜹ㅡ敥慢㠲捦扦愵㡡ち扢ち㍥㉥づ慡攲晣㐴㔵㥣攷㈸㝣㍦戲挶㈷捡㔲挵㝣戳ち㜹慣散慢㠲て㤲愵㡡搳敤㉡昸摣㌵愸㡡㈵㠹慡㔸散㈸㝣扦㘸挶㐷戳㔲挵㈲戳ち㜹㍥换㉡㕣挷〸㥦挸㑡ㄵ㑢散㉡昸〰㌳愸㡡搳ㄳ㔵戱挰㔱昸㝥㍥㡣捦㌸愵㡡ㄵ㘶ㄵ昲愰搳㠷〵ㅦ㙤㑡ㄵ攷摢㔵昰㐹㘰㔰ㄵㄵ㠹慡㤸攳㈸㝣扦搵挵㠷㠵㔲挵㈵㘶ㄵ昲挴搰㔷〵㥦ㄱ㑡ㄵ㤷搹㔵昰㤱㕡㔰ㄵ㌳ㄳ㔵㔱散㈸㝣㍦㡣挵愷㙥㔲挵㑡戳ち㜹昴收敢〸ㅦ戶㐹ㄵ慢敤㉡昸㙣㉡愸㡡改㠹慡㠸㌸ち摦慦㔰昱昱㤵㔴戱捥慣㐲㥥㘱昹戰攰㔳㉢愹攲〶扢ち㍥攴〹慡攲挴㐴㔵㥣攰㈸㝣㍦昹挴攷㐰㔲挵㉤㘶ㄵ昲㌰挸㔷〵ㅦ晦㐸ㄵ户搹㔵昰㘹㐹㔰ㄵㄳㄳ㔵㌱挱㔱昸㝥㕦㠹て㔴愴㡡㝦㥢㔵挸㔳ㄵ㕦ㄵ㝣㡥㈲㔵摣㘳㔷挱挷づ㐱㔵㡣㑡㔴挵㐸㐷攱晢㌱㈳㍥㤹㤰㉡㌶㤹㔵挸攳〹㕦ㄵ㝣㈰㈱㔵㍣㘴㔷挱晢昷愰㉡〶㈵慡㘲愰愳昰晤㜲㄰㙦昱愵㡡㙡戳ち戹捦昷㔵挱㍢㝢愹㘲㡢㕤〵㙦㠴㠳慡攸㤳愸㡡摥㡥挲昷㌳㍤扣㔷㤶㉡戶㤹㔵挸つ戳慦ち摥㈲㑢ㄵ捦搹㔵昰㡥㌲愸㡡㉥㠹慡挸㜱ㄴ扥摦挴攱㑤愷㔴昱戲㔹㠵摣㜹戲ち搷戹㌳〵㈶㔲挵づ扢ち摥㥡〵㔵搱㈱㔱ㄵ敤ㅤ㠵敦〷㘸㜸昷㈶㔵扣㠹㐱晣挶㐴㙥攱㝣㔸昰愶㑤慡㜸ㅢ〳摣㡦昰ㅥ㈷愸㡡搶㠹慡㘸攵㈸扣扦昶ㄲ㙥愶㈳㝦㠸㠱戵㡢㘴㌷㐸㘶晡㈱愰ㅤㄲ晦捥㠸晤ㅤ搵㤸愰ㅣ慤㤴敦㘲捦㐲捤改㠵㥣㔲摤愰㤰昳㤶愳昲㐵搹昲ㄳㅦ㈵㌲ㅦ戹㈱扥慥扡㘲㔶戴㘲っ扥㝤ㅤ㕦㔲㥤㕢㕣敡㑣昵挵户戲昳㙢㠳昵ㄷ㈲㕢挲㜱㥡㝣愸㜰㕣〵扥㈱戹㝥攱挸㑡㝣挷㝢㐱㐶改昸㐸㉣ㄶ慤㈸晢㈷㑣昷挷っ㜱㝥扢〷㕥昶户㔸〷㑥捥收慣㙢敦ㄷ㈸ㅢ㕦㘴扦てて晤㘳〶愹晣㤶敢扦㌷搹㕦㔶愰愴慡收攸戳㍣敥搸摢攵㘰㤹㤳㡣㙦捥挶㡦㕢戱愳㑡敡㔵㤸晥晣㌱扢㕣㡤攲㠴愴㠴戳挱换摥昵㈹ㄵ㥦㤱㝣づ㤲愹㕡㠳㜲㍦㜰㠲ㅦ㄰ㄸ晣㑢㌱㡤〷晦㑡摢㍢挱摢㠱㤷攰摦㔰昱㉤挹㜷㈰㤹慡〳愸ㄱ扣㘱㘰昰ㅦ挴㌴ㅥ晣㐷扡ㅢ㤵㜷〶㉦挱㝦愶攲ㄷ㤲㕦㐱㌲㔵ㄷ㔰㈳㜸㕡㘰昰㍦挴㌴ㅥ晣㑦扡ㅢ挱㝢㠱㤷攰㈹㔸㠷㘲㈹㤲㔴㤰㑣搵挷ㅤ晣昷㥦㠳㌰㑦ㄷ搳㜸昰㄰摤㡤攰〳㜴昰っ㉡㉣㤲㑣昱ㄸ攴づ晥㝤㘰昰㐶㘲ㅡて摥㤸敥㐶昰ㄱ㍡㜸㤸㡡晤㐸昶ㄷ㡦㔱敥攰㕦〴〶㍦㔰㑣攳挱て愲扢ㄱ㝣扣づ摥㡣㡡㠳㐹づㄱ㡦㠹敥攰ㅦ〵〶㙦㈱愶昱攰㉤改㙥〴㥦愶㠳㘷㔳搱㡡愴戵㜸㥣攸づ晥㙥㘰昰挳挵㌴ㅥ晣〸扡ㅢ挱㑦搳挱摢㔱搱㥥愴㠳㜸㑣㜷〷㝦㌵㌰昸搱㘲ㅡて摥㠹敥㐶昰㈲ㅤ扣㌳ㄵ㌹㈴㕤挴㘳愶㍢昸昶挰攰摤挵㌴ㅥ扣〷摤㡤攰戳㜵昰㕥㔴昴㈶改㈳ㅥㄵ敥攰㑦〵〶敦㉢愶昱攰晤攸㙥〴㥦慦㠳て愰㘲㈰挹㈰昱㌸摤ㅤ晣㤱挰攰㐳挵㌴ㅥ㝣ㄸ摤㡤攰㡢㜴昰ㄱ㔴㡣㈴ㄹ㈵ㅥ㑢摣挱敦ぢっ㝥扣㤸挶㠳㡦愵扢ㄱ㝣㠵づ㍥㥥㡡〹㈴ㄳ挵攳㝣㜷昰㡤㠱挱㈷㡢㘹㍣昸ㄴ扡ㅢ挱㉦搱挱愷㔱㜱〲挹㠹攲㜱㤹㍢昸㑤㠱挱㑦ㄱ搳㜸昰㔳改㙥〴㕦愹㠳㥦㐶㐵㠴㘴扡㜸慣㜶〷扦㌶㌰㜸㔴㑣攳挱ぢ改㙥〴㕦愷㠳ㄷ㔱㔱㑣㌲㔳㍣㙥㜰〷扦㈲㌰㜸愹㤸挶㠳㤷搱摤〸㝥㡢づ㍥㥢㡡㌹㈴ㄵ攲㜱㥢㍢昸㠵㠱挱慢挴㌴ㅥ㝣㉥摤㡤攰晦搶挱攷㔳戱㠰攴㜴昱戸挷ㅤ㝣㘹㘰昰㌳挵㌴ㅥ晣㉣扡ㅢ挱㌷改攰㡢愸㔸㑣戲㐴㍣ㅥ㜲〷㕦ㄸㄸ晣㕣㌱㡤〷㕦㐶㜷㈳㜸戵づ扥㠲㡡昳㐸捥ㄷ㡦㉤敥攰戱挰攰ㄷ㠹㘹㍣昸挵㜴㌷㠲㙦搳挱㉦愱攲㔲㤲换挴攳㌹㜷昰㤲挰攰㔷㡡㘹㍣昸㔵㜴㌷㠲扦慣㠳慦愴㘲ㄵ挹㙡昱搸攱づ㕥㄰ㄸ晣㍡㌱㡤〷㕦㐳㜷㈳昸㥢㍡昸㍡㉡慥㈷戹㐱㍣摥㜶〷㍦㌹㌰昸㝡㌱㡤〷摦㐰昷㝤挱搳㍦㐴㡣㘳ㄳ㕦愲ㅡ㉢挴㍡㘲㠱㈲㝥攴㈷㕡㠰慢捣搹昸㔱慣〵㐳换㘲ㄵぢㄸ戸ㅥ㝥㜶㈳㕤㔶㤷愵愵昶昹㝢戱㜸慤摡〲愱昸㤷㍥つㅢ昲晦ㄱ㠷㌷〴晢搶㘱㌲攲㜱昸换㐸つ㈹㕥㥡㜳㠳搵㔴㘴㘰㤶扥愲㔰㙡户㔶㑣㜱ㄴ晤愱戰㙥〷㔶改扣敥慢昵〵㈸㔳晦捤㐵㥢ㅢ㤱㑣昱慡㔲敥㘷敥〰㐷㘸昹愷㍥搵搵㑤㜴慡搳摢挳换㑣搹㥥〹㥥敤昹㕣㉢挶㥢摢㜳㌷㔳昰㔲㤳摢㘴摤㐳㡥㔷㥡㤲昰㕥㌳攱㌷摡㝤㡣㈷㈱㉦㍤㈵攱㘸㑦挲敦戴㘲㤴㤹昰㐱愶攰攵愷㈴摣㐴㡥㔷㥦㤲㜰戳㤹昰㘷敤㍥捣㤳㤰㤷愳㤲㜰愸㈷攱慦㕡㌱挴㑣昸㈸㔳昰㤲㔴ㄲ㍥㐶㡥㔷愴㤲昰㜱㌳㘱ちㄸ㠹㍢挰㤳㔰㘹㐵㝦㑦挲㔴慤攸㘷㈶㝣ㄲ㔲㤵づ㈲〹㥦㈲ㄷ㈲攱敥戳ㄵ㠳㜸て㌳挰㐸挲㍥㥥㠴㤶㔶昴昶㈴捣搴㡡㕥㘶挲㘷㈱㔵㡤㐰㈴攱㜳攴ㅡ㤳㌰攱昳ㄸ挴ㄳ㠶挱㐸挲㙥㥥㠴晢㘹㐵㔷㑦挲晤戵愲㡢㤹昰㈵㐸搵㠱㈰㤲昰㘵㜲〷㤱㌰攱㉢ㄸ挴ㄳ㌶〳㈳〹㍢㜹ㄲㅥ慣ㄵ㐷㝢ㄲㅥ愲ㄵ㐷㤹〹㕦㠳㔴戵〰㤱㠴慦㤳㙢㐹挲㠴㙦㘰㄰㑦㤸つ㐶ㄲ戶昳㈴㙣愵ㄵ㐷㝡ㄲ戶搶㡡㈳捣㠴敦㐰慡づ〷㤱㠴敦㤲㍢㠲㠴〹摦挳㈰㥥戰ㅤㄸ㐹搸摡㤳戰扤㔶戴昲㈴散愰ㄵ搹㘶挲㕤㤰慡愳㐱㈴攱㙥㜲㥤㐸㤸昰㍦ㄸ挴ㄳ㜶〶㈳〹㥢㝢ㄲ收㘸挵愱㥥㠴㕤戴攲㄰㌳攱㈷㤰慡敥㈰㤲昰㔳㜲㍤㐸㤸昰㌳っ攲〹㝢㠱㤱㠴〷㜹ㄲ昶搶㡡〳㍤〹晢㘸挵〱㘶挲㉦㈱㔵㝤㐱㈴攱㔷攴晡㤱㌰攱搷ㄸ挴ㄳづ〰㈳〹挳㥥㠴〳戵㈲换㤳㜰㤰㔶㌴㌶ㄳ晥ㄷ㔲㌵ㄴ㐴ㄲ㝥㑦㙥ㄸ〹ㄳ晥㠰㐱㍣攱〸㌰㤲㌰搳㤳㜰愴㔶㔸㥥㠴愳戴㈲挳㑣昸ぢ愴敡㜸㄰㐹昸㉢戹戱㈴㑣昸ㅢ〶昱㠴攳挱㐸挲㌴㑦挲〹㕡㔱捦㤳㜰愲㔶愴㥡〹晦㠲㔴㑤〶㤱㠴㈹ㄹ攰愶㔰挴㠴ち㕣㍣攱㌴敤晥攷㑦昶㥢㥣㝥户㌸㐱㉢晥㜰ㄴ晡摤敦㐴慤昸摤㔱挸扢㕦㍡㔳㥣〲㤵㈴っ㤱㍢ㄵ㥣㈴慣㙦㈶㍣㑤扢晦散㐹ㄸ搱㡡㥦㍣〹愷㙢挵㡦㘶挲〶㑣ㄱ㠵㑡ㄲ㌶㈴㔷〸㑥ㄲ㌶㌲ㄳㄶ㘹昷敦㍣〹㡢戵攲㕢㑦挲㤹㕡昱㡤㤹㜰㍦愶㈸㠵㑡ㄲ敥㑦慥っ㥣㈴㙣㘲㈶㥣慤摤扦昰㈴㥣愳ㄵ㝢㍤〹㉢戴攲㜳㌳㘱㔳愶愸㠲㑡ㄲ㌶㈳㌷ㄷ㥣㈴㍣搸㑣㌸㕦扢㝦散㐹戸㐰㉢昶㜸ㄲ㥥慥ㄵㅦ㤹〹㕢㌰挵㤹㔰㐹挲㤶攴捥〲㈷〹て㌳ㄳ㉥搲敥ㅦ㝡ㄲ㉥搶㡡て㍣〹㤷㘸挵晢㘶挲㌶㑣㜱㉥㔴㤲戰㉤戹㘵攰㈴攱攱㘶挲ㄵ摡晤㙤㑦挲昳戴攲㉤㑦挲昳戵攲㑤㌳㘱㝢愶戸〸㉡㐹搸㠱摣挵攰㈴㘱㐷㌳攱㈵摡晤㔵㑦挲㑢戵㘲愷㈷攱㘵㕡戱挳㑣㜸っ㔳㕣〹㤵㈴散㑣敥㉡㜰㤲㌰挷㑣戸㔲扢扦攸㐹戸㑡㉢㕥昰㈴㕣慤ㄵ摢捤㠴摤㤹攲㍡愸㈴㘱て㜲㙢挰㐹挲㥥㘶挲㜵摡㝤㥢㈷攱昵㕡昱㡣㈷攱つ㕡昱戴㤹昰㔸愶㔸て㤵㈴㍣㡥摣〶㜰㤲戰慦㤱㌰㡢搷挷㕣户㤶㍡㕦攵㥦㔶㜰摡㘹㍦㘷愵㘵ㅦ㤲㌶㙤㐰挳㔵ㅦ㍥户晢戲㔷㑦敥晢挹敦搷㕥晢敡㐷㤷㙤晦晤㤱改㝤㥦戹攱㠶愷㐶慤摤扥㝢晦挲㜵愹て晣㍣㘶摤挲㥣㔹ぢ攷ㄴ㑥敥㌰㝣攱〹㌳㈷攴㡣摦慦㘳扤㝡昵敢ㅦ搹㘴㕢戳㜶攱㐵㜳㌶愹㈷摥㙡㕡愶攴㥡㤸㈷戸㝥㐸换㔷㐳晣㠵敦㐰㕡㜹愶搸ㅦ㔲㙢〰㐸愳搴慣扢敢扡㤶㝢㌴〴〳捤㕡㜸搹㉣戵っ㘲㉤㠳敤㕡㜸搹㕢愷戸㙣搲戵っ㌱㙢搹慣㙢ㄹ捡㕡㠶搹戵㍣㕡搷戵㍣愶㙢ㄹ㙥搶挲㡢㙤挱㘵〴㙢ㄹ㘹搷挲㡢攵㍡挵㐵慥扦戱㡢㔸愳捣㕡戶敡㕡㐶戳㤶㌱㜶㉤捦搶㜵㉤捦㈱㠱ㅣ㌲挷㥢戵昰ㄲ㕤㜰ㄹ换㕡挶搹戵昰ㄲ扢㑥㜱㜹㔹搷㌲摥慣攵ㄵ㕤换〴搶㌲搱慥攵戵扡慥攵㜵㕤㑢慥㔹ぢ㉦散〵㤷㐹慣㘵戲㕤ぢ㉦捣敢ㄴㄷ戹搶攷晥㌲挵慣攵㍤㕤换㔴搶㌲捤慥㘵㔷㕤搷戲ㅢ〹㘴㝦㌹挱慣㠵户〳㠲换㠹慣攵㈴扢ㄶ㕥捥搷㈹㉥㜲㠷㐰㕣㑥㌶㙢昹㑣搷㜲ち㙢㌹搵慥攵换扡慥㐵㙥ㅥ㔸㑢㥥㔹ぢ㙦㈲〴㤷搳㔸㑢挴慥㠵㌷〱㜵㡡㡢摣㔷戰㤶改㘶㉤㍦攸㕡昲㔹㑢㠱㕤换㉦㜵㕤㡢摣㜲戰㤶愸㔹ぢ㙦㍤〴㤷㐲搶㌲挳慥㠵户づ㜵㡡㡢摣㡤戰㤶㈲戳ㄶ摥㤵㐸㉤挵慣㘵愶㕤ぢ敦㉡敡戴ㄶ戹㔱㘱㉤戳㤰㠹㉦戹㘶攰つ㡢搴㔲㠲㠱㔵ち㠲㙢〶摥㜰搴㘹㉤㜲て㠳ㄲ慣㌲㘴攲㑢㙡攱扤㡣搴㔲㡥㠱㌵ㅢ〴戵昰㕥愴㑥㙢㤱摢ㅢ㤴㘰捤㐱㈶扥愴ㄶ摥收㐸㉤ㄵㄸ㔸㤵㈰愸㠵户㈹㜵㕡㡢摣昹愰〴㉢㠶㑣㝣㐹㉤扣〳㤲㕡慡㌰戰收㠲愰ㄶ摥挱搴㘹㉤㜲㔳㠴ㄲ慣㜹挸挴㤷搴挲㥢㈳愹㘵㍥〶搶〲㄰搴挲㥢㥢㍡慤㐵敥㤷㔰㠲㜵㍡㌲昱㈵戵昰扥㐹㙡㌹〳〳㙢㈱〸㙡攱㝤㑦㥤搶㈲户㔲㈸挱㍡ㄳ㤹昸㤲㕡㜸㑢㈵戵㥣㠵㠱㜵㌶〸㙡攱㉤㔱㥤搶㈲㜷㔹㈸挱㕡㠴㑣㝣㐹㉤扣摢㤲㕡ㄶ㘳㘰㉤〱㐱㉤扣㕢慡搳㕡攴〶っ㈵㔸攷㈰ㄳ㕦㔲ぢ㙦挴愴㤶愵ㄸ㔸攷㠲愰ㄶ摥㐸搵㘹㉤㜲㙦㠶ㄲ慣㘵挸挴㤷搴挲㝢㌴愹㘵㌹〶搶ち㤰㐶愹㘱摥㐱㔱搸㈸㑤昱戶㐹㥥㐸捤㜳敥晡〶㐱㥥愱㔲ㄴ㙦愵㐴㌱搷㔱㠴愱戰㉥㠰㌴捣㥢ㅥ挷㥤㜷㍡㘲ㄵ昳戸昳敥㐷ㄴ㤵愶晢挵㜴攷㝤㡡攳㍥㔴㕢捤昱戸昳㠶㐵摣㘷㥢敥㤷搲㥤户ㄶ㡥㍢敦㈷挴慡捣攳捥㝢っ㔱㤴㥡敥㔷搰㥤㜷〳㡥晢㘸㙤㌵换攳捥摢〲㜱㥦㘹扡㕦㑤㜷㕥挰㍢敥扣㙡ㄷ慢㈲㡦㍢慦攴㐵㌱挳㜴㕦㑤㜷㕥㜳㍢敥ㄳ戴㔵搴攳捥㡢㙦㜱㉦㌰摤慦愳㍢㉦㤳ㅤ㜷㕥ㅢ㡢搵㜴㡦㍢慦㤷㐵ㄱ㌱摤搷搱㥤㔷戶㡥晢㔴㙤㤵攷㜱攷㈵慥戸㥦㙡扡摦㐸㜷㕥㡣㍡敥扣〲ㄵ慢㤳㍤敥扣㉡ㄵ挵㐹愶晢〶扡昳晡搱㜱㍦㐵㕢㥤攰㜱攷㠵愴戸㑦㌳摤㙦愵㍢㉦昹ㅣ昷搳戴搵ㄴ㡦㍢慦晤挴㝤戲改扥㤱敥扣㑡㜳摣昳戵㔵慥挷㥤㤷㙢攲㍥搱㜴扦㡢敥搱㝤敥㠵摡㙡扣挷㥤㔷㔸攲㍥捥㜴扦㠷敥扣ㄶ㜲戲昳〲㐸慣㡥昷戸昳愲㐸ㄴ㘳㑣昷晢改㍥㙢㥦㍢慦㔹挴㙡㤴挷㥤搷㌱愲ㄸ㘹扡㙦愲㍢慦㌸㥣散扣捣㄰慢攱ㅥ㜷㕥㝡㠸㘲㤸改晥㌰摤㜹㤱攰戸昳捡㐰慣㠶㜸摣㜹戵㈰㡡挱愶晢㘳㜴攷晢扡攳捥㌷㜳戱ㅡ攸㜱攷ㅢ扣㈸〶㤸敥㑦搰㥤㙦挵㡥㍢摦㝦挵慡㥦挷㥤敦挹愲攸㙢扡㍦㐵㜷扥㝢㍡敥㝣换ㄴ慢㘳㍤敥㝣ㅢㄵ㐵ㅦ搳晤ㄹ扡昳つ捦㜱攷扢㥣㔸昵昲戸昳㥤㑦ㄴ㍤㑤昷攷攸捥昷㈸挷㥤㙦㑣㘲搵摤攳捥㌷㉢㔱㜴㌳摤㕦愰㍢摦㔶ㅣ㜷扥㤷㠸㔵ㄷ㡦㍢摦㕦㐴㤱㘳扡扦㑣㜷扥ㄳ㌸敥㍣晤㡢搵㌱ㅥ㜷扥㈵㠸愲㤳改扥ㄳ㔲挵㤳扤㍣昶㝢㤵ㅣ捦摤挲扤㐶㡥愷㘲攱㕥㈷挷㌳慢㜰㙦㤰攳㠹㔲戸㌷挹昱扣㈷摣㕢攴㜸ㅡㄳ敥㙤㜲㍣㉢〹昷づ㌹㥥㘴㠴㝢㤷ㅣ捦ㄹ挲扤㐷㡥愷〰攱摥㈷挷㈳㕡戸て挸昱〰ㄵ敥㐳㜲㍣摥㠴摢㐵㡥㠷㡦㜰扢挹昱㘸㄰敥㍦攴戸㜳ぢ昷ㄱ㌹敥慢挲敤㈱挷㕤㑦戸㡦挹㜱㑦ㄲ敥ㄳ㜲摣㌱㠴晢㤴ㅣ晢㉣摣㘷攴搸㌶攱㍥㈷挷㉥〸户㤷ㅣ㐱ㄵ敥ぢ㜲〲㉡摦㔳扦〴愷㕦㑡挰昵㐹〵㘴㥦㔴挰昶㐹〵㜴㥦㔴挰昷㐹愵〹㍥愹㌴挳㈷㤵愶昸愴搲ㅣ㥦㔴㥡攴㤳㑡戳㝣㔲㘹㥡㑦㉡捤昳㐹愵㠹㍥愹㌴搳㈷㤵愶晡愴搲㕣㥦㔴㥡散㤳㑡戳㝤㔲㘹扡㑦㉡捤昷㐹㘵㈷昰㐹㘵㘷昰㐹㘵愷昰㑡挳㝡攷㘸昰晦〰摣㤵戸㉢ | 㜸〱捤㝤〷㝣ㄴ㘵晡㝦摥㤰㉣㤹愵㘴㍤ㅢ㈲㘲㔰ㄴ〵づ㌷挹㙥ち㠲ㄲ㍡㐸㙦㜶㘱换㉣㐴㔲㌰㔹㄰慣㘰㍦摢㘱㔷㔰挱晡戳㥤愲㘲搷㌳㜲搶ㄳ㍤㝢敦㝦ぢ㈷㥣愷愷愷攸㔹晥摦敦昳捥㙣㘶㜶㘶㤷晣晣㕤㍥ㅦ㐳昶㘱㥦晥捣昷㤹㥤㥤㜷收㝤㌳〵慡愰愰攰ㄷ晣昰㝦晥ㄴ昱㑤㥦㤹换㕡搳㘶攳㤰㔱捤つつ㘶㈲㕤摦摣搴㍡愴慥愵㈵戶㙣㔲㝤㙢扡ぢっ〲㜳敢愱㙦㉤㥥摢㕡㝦㥣㔹㌲㜷㠹搹搲ち愳攲㠲㠲㤲ㄲ愳㄰晡㕤慣㔷挸㘶っ㝡ㄹ㐵㈴戰㉡㌰〲㈴㕤㐹㑡㐸っ㤲㈰㐹㌷㤲敥㈴㍤㐸㝡㤲㤴㤲㠴㐸戶㈳昹ㅤ挹昶㈴㍢㤰散㐸戲ㄳ挹捥㈴扤㐸㤸摦攸㑤戲㉢㐸昷㍥㈰戳㐶㡤㥣ㅡ㍦ㅡ㕢㌳㌳摤摣㘲づ㉥㥢愳㙢ㅥ㕥㕥㍥愴㝣㐸㐵㘵㙤昹㤰昰攰戲㔱㡢ㅢ搲㡢㕢捣攱㑤收攲㜴㑢慣㘱㜰搹戴挵昱㠶晡挴㐱收戲㔹捤ぢ捤愶攱㘶㍣㕣ㄹ㡦㐵㙡捡㈳搱㘸慡戶戶愶晢㙥㠸㍣㘵搴挸㘹㉤㘶慡昵扦ㄵ戳㉦㘳㑥ㅤ㌵㜲挸ㄴ㌳晤摦㡡戹㍢㘲㈲攴攸收挶㔸㝤搳㝦㈹㘸㌱㝢㕡㌹摡㑣搴戳昹愶搹㔲摦㌴㝦〸捡㜶〱つ慥㝡挸㔸㈰㥥㠸戵愶㐷㤹つつ㌳捣ㄴ晢摥扤㤱㤸㤹㉤㘶㔳挲㙣敤搹㌸㘶㘹挲㙣戰搴慤㈵㡤㜳㘲㉤㔳㘲㡤㘶ㄱ摦㤴㌶敡扥㑤㐸㥡㑤改晡昴戲ㅥ㡤戳㕢捤ㄹ戱愶昹㈶㑤㡡ㅢ挷㉤慥㑦ㄶㄵ愹愲愲㠲㉥〳晣㡡㤱摥っㄹ摢㤲ㄸ戵㈰搶㤲ㄶ㡥㕤㉢昷戳㜵散㈱㔲戸慢㉣敥㐵㘵㔹㕥㙣搳捣晡挶㠳捣㤶㈶戳㠱㐹搸扣㐱㔹㐶㠲㠹㠶㍥〳㡥扤㌵㙣㡣敡㘶㝤摥戸㈹捣㘲㤴㤱昴〳〹散〱搲㜵㜸㕤昹搰㐸敤㔰㘳㑦㡡晢㠳愸愲户昱㤹㜵扡昱㜳㔳㌸㌷㔶㌸㌷㕥㌸㌷㔱㌸㌷㔹㌸搷㉣㥣㥢㉡㥣㍢扦㜰敥㠲挲戹昵㠵㜳㡦㉥㥣扢㄰㌶昶㑦㐹搷慥㠵搶捦㍥㌷摣㜸摦㐱㉦㈴挶㥦㜹昱昴㤱㤷㍦㝦挹挷㡡ㅦ㔳昹扣敥㡤㌷挶〰㤰挰㍥㈰扡㡣昰㔰㘳㕦㡡〷㠲㈸昵㉡捡㘰㈹摦敥昱搶㤱户摣㍡㜸挴㙤〳㑦ㄹ晥昳愰㔱㥦㉢㝥捡㈵挶㘰ㅡ晦ㅥ㈴㌰〴㐴㘲㐴ㄱ㘳㍦㡡挳㈰㑡晤捤㡡昱挶〵㠹户捥㍦敥攲㐹㌷扤㔷戸戱昱㥢㈷昷㔵㍣㐸㐸㡣ちㅡ㔷㠲〴㈲㈰扡㡥㡡愱㐶㤴攲㉡㄰愵㥥戱㘲慣㕡㜹挹〷ㄳ扦晥㘰摣慡慦挶㕤戵㈲戵昵㜸挵㝤㑤㘲搴搰戸ㄶ㈴㌰ㄴ㐴搷㔱㌹搴搸㥦攲㘱㈰㑡晤挵㡡搱㔸㌰㘲挴愰敦戶㑣扤㝣搳愹昵㉦慤㕦㤶㔶㍣㐴㐹㡣〳㘸㝣㈰㐸㘰〴㠸㡥ㄱㄹ㙡搴㔱㍣ㄲ㐴愹㐷慣ㄸ㔵敢ㅥ㥡晣㑡慦户づ扡昱摡㑢捥ㄹ㝦散摤〹挵㈳㥣挴ㄸ㑤攳㌱㈰㠱戱㈰㝡㕢㔰挷㌸㡡挷㠳㈸㜵㥦ㄵ攳捥敦户㝥㜸搱愰挷愶㥥㌷扢㔷改挶㜱晦ㄹ愵㜸㠰㤴ㄸㄳ㘹㝣㄰㐸㘰ㄲ㠸㡥㔱㌵搴㤸㑣昱ㄴ㄰愵敥戴㘲昴㤹㌶戸晢摡㝦晥愵敥㤶㠳て㝢敦㡥㝦㡥攸慦戸㥦㐸㡣㘹㌴㥥づㄲ㤸〱㈲㌱㉡慢㠷ㅡ㌳㈹㥥〵愲搴慤㔶㡣搴て㍤㙥晦㝥昳扡㠹㉢晡扣㌳散愵㘷㑦㥣慤㜸㜸㤶ㄸ㜳㘸㝣㌰㐸攰㄰㄰㕤〷㘲ㅣ㑡昱㘱㈰㑡摤㘰挵㔸㝤捤㝢扦㜴㝦昷搲㈹㤷捥㝢㜷㠷挶搵㠷㉦㔱㍣扡㑢㡣㈳㘸㝣㈴㐸攰㈸㄰㠹ㄱ挵慥㍥㤷攲㜹㈰㑡慤戱㘲㡣㍡晡挷摢㡥晦昶戵挹㜷摥昲挳㠰挱昱ㄵㅢㄵ扦ㅣ㈴㐶㥣挶〹㤰㐰ㄲ㐴挷〰ㅥ㈶挵㈹㄰愵慥戰㘲㔴㙥ㅡ戹敦晡㤵㕢愶㕥㍢㙢昷收㌷㙦㕦戵㔴昱扢㐵㘲㉣愰㜱㍤㐸攰㘸㄰ㅤ〳晢ㄸ㍦㌳㐶〳㠸㔲ㄷ㔹㌱挶㥦㝣搱〳慢㝦㕣㌵攵昶昰㘱㠷敥扥㐳挹ㄱ㡡㕦㑤ㄲ愳㠹挶捤㈰㠱㐵㈰㍡㐶捤㔰攳ㄸ㡡㕢㐰㤴㍡捦㡡戱晢扡摤戶晥晤戶㝢て㝡㈴㝥晣㉤㤳て㍦敥㍦㡡摦㙣ㄲ㈳㑤攳挵㈰㠱㈵㈰ㄲ㈳㔲㍥搴㌸㤶攲愵㈰㑡㥤㘹挵㌸昸敢搱〳ㄷ戵㕣㍤㘵戵扡改晤〱收㥡㈳ㄴ扦ㄸ㈵挶㜱㌴㍥ㅥ㈴㜰〲㠸慥㈳㍡搴㌸㤱攲㤳㐰㤴㕡㘱挵㔸㔷扥㙥㙢㥦ㅢ㙦㥤㝡捦戲㠹㌷㍤㜵昴㐵㔳ㄵ扦㔷㈵挶㜲ㅡ慦〰〹㥣〲愲敢挰扥㝥㉡挵愷㠱㈸㜵扣ㄵ㘳摣晢㜷㙦昷㑥戰㘱搲㈹〵㘳㕦㌴扡晣昴戹攲搷戲挴㌸㠳挶㘷㠲〴捥〲㤱ㄸ㔵昸散晦㠱攲戳㐱㤴㕡㙣挵㌸慣㌵㔴扤敥搵愳愶㥣戹换敢㝤㤷ㅣ㌵㘹㤳攲户扡挴㌸㤷挶攷㠱〴捥〷㤱ㄸ㤵搸㍦晥㐸昱㑡㄰愵㥡慤ㄸ㑢㙢㑦慡扢晢晢晢挷㥦扥攲㥤戹㉦捣㤹昲愴攲㐹㠱挴戸㤰挶ㄷ㠱〴㉥〶搱㜸〰搳㑢㈸扥ㄴ㐴愹㝡㉢挶愴摤㝥㝡㌶㔹㍢㜵摣愹晦搳㍦㝥㕥搵㍦〳㡡攷ㄴㄲ攳㜲ㅡ㕦〱ㄲ㔸〵愲昱〰愶慢㈹扥ㄲ㐴愹㠴ㄵ攳愲㠶㤲㜵慢て摤㙥攴㙤㉢摢㡥㉥ㅣ晥敤扢慡ㄷ搴ㄲ攳㙡ㅡ慦〱〹慣〵搱摢㠲晤昴ㅡ㡡慦〵㔱敡㐸㉢挶晥戳慥愸晤㙣㔰摤攴㠷て㔸晦攵搳㌷㙣扥㑥昱㡣㐶㘲㕣㑦攳ㅢ㐰〲㌷㠲攸㙤挱㘷敥㝦㈸扥〹㐴愹㠳慤ㄸ㥦㡥㔳㑢ぢ敢敦㥣扣晡㠳昳てぢ〶愶㕤愰㝡㐳㉤㌱㙥愱昱慤㈰㠱摢㐰昴戶㘰㍦晤ㄳ挵户㠳㈸㌵摤㡡戱挷昶昷慥㝡㝣搹㉥㜵ㄷ敤晡搴扣扡㈵㉢㍥㔷㍣㥦㤲ㄸ敢㘸㝣㈷㐸攰㉥㄰扤㉤㠸㜱㌷挵敢㐱㤴㍡挸㡡昱挴愶㉥㐷㥥昱挴攳㘳搷㐴敢ち捦ㅡ户昲昵敥昷㐲㍤摤晡捡ㅢ摤ㄲ㍢ㄶ攷つ敤愷㈴ㄵ㐳挲晣户敤㜳㌱㥣㡡愵愲愹敡㔴㜹㜹㌲ㅡ㡥㔵挶㡡换㄰戶愳㘷〰摣㐵扢愷づ慥㙦㑡㌶ㅦ㉢愷〴摤㔳㘳敢ㅢ搲㘶㡢㌰愵㈹晣愷㑦㙢㠴敦㤱ㅡ戳ㄴ攷㠳〹㝤昶戰㐳㙡㤴搹㤲挶㜹㔴㝡㔹晢㈹㐵㥦㤱戱㔶戳㥤ㅤ㘴挵ㅥ搹扣戸㈹搹扡慢扦㜲㘶㍡㤶㌶㝢㘷敢摡㠳㜸摣㘶攲ㅣ换㙣㤵㤲晡㘶扢捤㠹㌵㉣㌶敢㤶搶㙢昵㙥㔹㙡㥣㙤㌵挷㜳㙢挷戶㤸挷㘴戴㥥㡡敡㌰〴㔸㈲戱㍤㕢愹㔵扡慥戲㔱ぢ㥡㕢捤㈶㈹㙦㔰攳戴晡挴㐲戳㘵愶挹〱㠴㤹㤴㑤摤㤱㉡敢㤴㙦搰搴㈶㙣㈸㑥攲㤲㝢㌸愵〴摡㙣㑡㥡㐹搴扢〸㈸㉦㥢ㄵ㡢㌷㤸㍢戹㑣㜴㑥㈸㜶㜱㠹挷㌶㈷ㄶ户㡥㙡㙥㑡户㌴㌷戸㌵㜵挹㈵㌱㥣㘶㈶㈷㌷㈷捤㈲昹㈹搰㔴ㄵ㜴改愲㔴挱㍥㝥攷㙢㡣摤捡㌳㍡挷㑥挲昳挶晣挶㡥㥤㠸挶扥㘷㠲㤹挸㜸攳搸挹㘸扦㙦摥㑡㥣㍢㈱慤挳㜹慤㝤㜶㔲㍡昵㜲㝦昰㠶捣㐰㝦搰㠷〶㤳㥦捡挲晥戹㐳戶敦㤷摢愸搴搱ㄵ㡥ㄷ㘹㥤〷㌴〹㥢搹昷㍡搷戸戰㜰㝢㙢敢挷㉣挱㘰㘲㝣慣㈹搹㘰戶攴ㅤ敤㉡㔶㘴摣㐷㜲㍦挹〳㈴て㤲㍣〴㔲㍣ㅡ挷戸㥣㠸ㄶ挱㐲㉤㔵换㡡㡦慤㑦愶ㄷ〴ㄶ㤸昵昳ㄷ愴㈱挳㈸戹愴㠴㜰㝢㝥㡣㐷㈰㌲晥㑣昲㈸㐸㌰㔸㄰㘸挳晦〵㠱愰昱ㄸ晥〳㕦摣て晦晦敦挷㉥㠵昰㌲㘴愸㠴戱㙣㙢㜱㈳㐶㘴慤㕤扡昸㙤昹昸㔸敢㠲㌴㍦㜴昹㤵㡣户㠱攴㉦㈰摤ㅦ〷㤹㌲摥㙣挰㐷昶扦㌵っ㉥摥ㄳ㌱户㌹摣攲㈹捦㑥㡤㌳㤷㌵㈵ㄶ戴㌴㌷攱㘲挴攸㔸㍡㔶㤷挰㤸戲㔵挵〲㡤㤳㥡㐷㉤㑥〷ㅡ挷搷攳扦敥㡤㌳捣㐵㘶㉣㍤ち㠷攴㜴㡦挶㐹ㄸ㡦捡㌱㜳㐲㜲㘹㜱愳ㅥ㑡㡥㌶㕢ㄳ〶挷㥣ㄳ㜰〸㕡ㅡ挰㍢ㅣ㔳扢㌷昲愰㘲㉥㑤㌳㜴搷挶㘹㌱㡣㔹搳〶㡣〶㠹㤷㝥㐷捦ㅥ㈲戳扤㠳ㄶ㠷〸㈱㜹敢㠸搲㑤〴㍡㔲〱昷ㄲ㝣㕢攲㙢戵挸愲搹㥦㤶搹改晡㠶搶㈱ㄶ扣㐳㐶㌷攳㥡㠴㈹㤷㘳〸㝢㈰㠰㥤㈹㤰户㔹搹ㅦ㙡づ㕡愷㈶攲㍡㉣㑡ㄹ搷搲扣㜸㔱㕦挴晡㙦挵㘱慣〲攳〹㤰㌵㕦摤戲晦㕥㔷摤昱㡢昵晦挹昸戸挸㡦戱〷㉤摡㐰挸攲㍦昹㌱㥥挶㝦挱㝣扡攲晥戰昰㍤慡收ㄸ㕦ㄷ挳扥㝢㈳戶㜶㔶㡢㈹ㄷっ㑡㠴㔹戶挸散搱㜸㜰㜳换挲㜸㜳昳㐲㌶扦愷㜰慤ぢ㑣㌳捤㔱㜸㌷敢愲〳摦㉢愵扡㜴㜱㡤戵ㅤ挳昵摤ㄱ㍦戰ㄱ愴㐷㕤㐳㐳㤹ㅤ戱㌵昰ㅣ㐴㕤昰敤ㄱ㜸ㅥ㙦㐲㔵攱捡㐸昵㉣㕥㘹ちて㔹摡搰摡愸捡戱搵ㅣ㌷摦扣昹捤改㐷㜵㝦慦敥捡㠹㔷摥戰捦挰搹扢愹戰愵昰っ捡昷㐶㥣㌲扣㡣ㄷ㐹㕥㈲㜹㤹攴ㄵ㤲㔷㐱搴㐰戸昲㜸㠴昷敥ㅦ攳㜵昰挶ㅢ㈴㙦㠲攰㈸㈲挸攳愰昲戶㘶搵〰晣捦〳㡢昱づ挹扢㈰㡡㠳㝣㝥〴ぢ㡣昷㐰㜲昶㜱ㅦ㕡戴㠱㈰㜱㈶戳昱㈱〴㐱㈳㡦㑥つ㠴〵㝢㘹㄰㍢㠳㘸ㄹ㐴㑡昵㐲ㄸ㕦㘰㜶戶ㄴ㥥㉢つ㠳攱㔶㐶晦捦㐹㌶㤳㙣㈱昹〷挹ㄷ㈰㙡㍢戸晡〳昳㈵㙤扥㈲昹ㄷ㠸〳㤸㙦㌴慢㝥㡦晦〵㤸㝦搳攸㕢㄰戵ㅦ㠸〶收㍢扣换〹捣㄰㍡戴㠱㈰㜹㍢㌰㍦㐰㄰㌴昲攸㔴ㄸㄶ㝥挰晣昲㜳づ㘰㝥戶ㄴ㥥换㈷ㄵ㠸㔴㠶㤷搱㐵㠱昰挲慥㔱㑣ㄲ㈰改ち愲戶挲搵ㅦㄸ㠳㌶㐱㤲㙥㈰づ㘰㝡㘸㔶㔵㈲㜰㍦〶敦㐹愳㔲㄰ㄵ〵慢㠱〹㠱捤〹㑣㠴㕥㙤㈰㉥㘰戶㠷㑢搰挸愳㔳㔵㜰昱〳收搳㕣挰㝣㘲㈹㍣搷㠴㙡㄰愹っ㉦愳て㤲ㅡ扢㤱昴㈵搹㥤愴っ㐴扤㥦ㄳ㤸㍤㘸戳㈷㐹㝦㄰〷㌰㝢㙢㔶搵㈲㜰㍦〶ㅦ㐰愳㝤㐰搴晥㘰㌵㌰晢㠲捤〹捣㔰㝡戵㠱戸㠰ㄹっ㤷愰㤱㐷愷㠶挱挵て㤸攷㜲〱戳搱㔲㜸㉥㜴ㅤ㠰㐸㘵㜸ㄹ㔱㈴㌵慡㐸慡㐹㙡㐸㙡㐱搴㤳㌹㠱搹㥦㌶挳㐸㠶㠳㌸㠰㌹㔰戳敡㐰〴敥挷攰㈳㘸㔴〷愲敡挰㙡㘰㐶㠲捤〹捣〸㝡戵㠱戸㠰ㄹ〳㤷愰㤱㐷愷㐶挲挵て㤸昵戹㠰戹摢㔲㜸慥摥㡤㐶愴㌲扣㡣㈹㐸㙡㑣㈵㤹㐶㌲㥤㘴〶㠸晡㔳㑥㘰㘶搱㘶㌶挹ㅣ㄰〷㌰㠷㘸㔶㡤㐱攰㝥っ㝥㈸㡤づ〳㔱扣ㅡ愸㠱㌹ㅣ㙣㑥㘰挶搲慢つ挴〵捣㔱㜰〹ㅡ㜹㜴㙡㍣㕣晣㠰㔹㥤ぢ㤸㔵㤶挲㜳㐹㜲㈲㈲㤵攱㘵捣㐷㔲㘳〱㐹㍤挹搱㈴ぢ㐱搴挵㌹㠱㘹愴㑤ㄳ㐹㌳㠸〳㤸㘳㌴慢づ㐲攰㝥っ摥㐲愳㔶㄰㌵ㄹ慣〶㈶つ㌶㈷㌰㤳攸搵〶攲〲收㔸戸〴㡤㍣㍡㌵〵㉥㝥挰㥣㤲ぢ㤸ㄵ㤶挲㜳㥤㜵ㅡ㈲㤵攱㘵㉣㐷㔲㘳〵挹㈹㈴愷㤲㥣〶愲㡥捦〹捣ㄹ戴㌹㤳攴㉣㄰〷㌰㘷㙢㔶㑤㐷攰㝥っ㝥づ㡤捥〵㔱㌳挱㙡㘰捥〳㥢ㄳ㤸ㄹ昴㙡〳㜱〱戳ㄲ㉥㐱㈳㡦㑥捤㠲㡢ㅦ㌰昵戹㠰㔹㘰㈹㍣ㄷ㡦攷㈰㔲ㄹ㕥挶ㄵ㐸㙡慣㈲㔹㑤㜲㈵挹㔵㈰㉡㥥ㄳ㤸㌵戴㔹㑢㜲つ㠸〳㤸敢㌴慢づ㐶攰㝥っ㝥㍤㡤㙥〰㔱㠷㠲搵挰摣〸㌶㈷㌰㠷搰慢つ挴〵捣捤㜰〹ㅡ㜹㜴敡㌰戸昸〱㌳㉤ㄷ㌰㔳㉤㠵攷㡡昸ㄱ㠸㔴㠶㤷㜱ㄷ㤲ㅡ㜷㤳慣㈷戹㠷攴㕥㄰㌵㈱㈷㌰昷搳收〱㤲〷㐱ㅣ挰㍣慣㔹㜵㈴〲昷㘳昰㐷㘸昴㘷㄰㌵ㄷ慣〶收㔱戰㌹㠱㌹㡡㕥㙤㈰㉥㘰㌶挰㈵㘸攴搱愹㜹㜰昱〳愶㍡ㄷ㌰㔵㤶挲㜳㤹㍦㡥㐸㘵㜸ㄹ捦㈲愹戱㤱攴㌹㤲攷㐹晥〶愲挲㌹㠱㜹㤱㌶㉦㤱扣っ攲〰收㔵捤慡〴〲昷㘳昰搷㘸昴㍡㠸㌲挱㙡㘰摥〰㥢ㄳ㤸㈴扤摡㐰㕣挰扣つ㤷愰㤱㐷愷㔲㜰昱〳愶㙦㉥㘰㜶戳ㄴ㥥㝢ㄷぢ㄰愹っ㉦攳㘳㈴㌵㍥㈱昹㤴攴㌳㤲㑤㈰㙡攷㥣挰㝣㑥㥢捤㈴㕢㐰ㅣ挰㝣愱㔹挵㕢㈱晤ㄸ晣㥦㌴晡ㄲ㐴㉤〴慢㠱昹ち㙣㑥㘰㡥愶㔷ㅢ㠸ぢ㤸㙦攰ㄲ㌴昲攸㔴〳㕣晣㠰㈹捥〵㑣㤱愵昰摣㤰㘹㐲愴㌲扣㡣㥦㤰搴昸㤹攴ㄷ㤲㠲㐲㄰〵愲㝥晥㈹搷㤹㙦ㄷ摡ㄴ㤱ㄴ㠳㌸㠰改慡㔹搵㡣挰晤ㄸ扣㠴㐶㥣敥愰㡥〱慢㠱〹㠲捤〹捣㈲㝡戵㠱戸㠰改挱戸㐶ㅥ㥤㙡㠱㡢ㅦ㌰㕢戰ㄱ扥㘳愵捤㤶挲㜳㤷㈹㡤㐸㘵㜸ㄹ㍢戱昶㥤㐹㝡㤱散㐲搲ㅢ㐴㝤㤲ㄳ㤸㍥戴搹㡤愴㉦㠸〳㤸㌲捤慡挵〸㉣挰昴愳搱ㅥ㈰敡㔸㠸㌴㌰㝢㠲捤〹捣ㄲ㤶搴〶攲〲㘶㙦挶㌵昲攸搴㔲戸昸〱昳㜲㉥㘰㕥戲ㄴ㥥㕢㘷挷㈱㔲ㄹ㕥挶㝥慣㍤㑣㔲㑥㔲㐱㔲〹愲㌶收〴㈶㑡㥢㉡㤲㙡㄰〷㌰戵㥡㔵挷㈳戰〰㌳㤴㐶晢㠳愸ㄳ㈱搲挰っ〳㥢ㄳ㤸ㄳ㔸㔲ㅢ㠸ぢ㤸〳ㄹ搷挸愳㔳㈷挱挵て㤸〷㜳〱昳㠰愵昰摣て㕣㡥㐸㘵㜸ㄹ攳㔹晢〴㤲㠹㈴〷㤱㑣〲㔱㜷攷〴㘶ち㙤愶㤲㑣〳㜱〰㌳㐳戳㙡〵〲ぢ㌰㌳㘹㌴ぢ㐴㥤ち㤱〶㘶㌶搸㥣挰㥣挲㤲摡㐰㕣挰ㅣ〲㤷愰㤱㐷愷㑥㠳㡢ㅦ㌰搷攴〲㘶慤愵昰摣攴㍣〳㤱捡昰㌲㘲㐸㙡挴㐹ㄲ㈴㐹ㄲㄳ㐴慤捡〹捣㝣摡㉣㈰愹〷㜱〰戳㔰戳㡡昷㑣〵㤸〶ㅡ㌵㠲㈸摥㌴搵挰㌴㠱捤〹捣㔹㉣愹つ挴〵捣㌱㡣㙢攴搱愹戳攱攲〷捣㔹戹㠰㌹搳㔲㜸敥摣㥥㡢㐸㘵㜸ㄹ挷戱昶攳㐹㑥㈰㌹㤱攴㈴㄰戵㈲㈷㌰换㘹戳㠲攴ㄴ㄰〷㌰愷㘹㔶㥤㠷挰〲捣改㌴㍡〳㐴晤ㄱ㈲つ捣㤹㘰㜳〲㜳㍥㑢㙡〳㜱〱㜳㌶攳ㅡ㜹㜴㙡㈵㕣晣㠰㘹捥〵㑣㤳愵昰摣㡥扥㄰㤱捡昰㌲㉥㘲敤ㄷ㤳㕣㐲㜲㈹挹㘵㈰㙡㐱㑥㘰慥愰捤㉡㤲搵㈰づ㘰慥搲慣扡〸㠱〵㤸慢㘹戴〶㐴㕤〲㤱〶㘶㉤搸㥣挰㕣捣㤲摡㐰㕣挰㕣挷戸㐶ㅥ㥤扡ㄴ㉥㝥挰捣挹〵捣㙣㑢攱戹挷㝥㌹㈲㤵攱㘵摣挶摡晦㐴㜲㍢挹ㅤ㈴敢㐰搴搴㥣挰摣㐵㥢扢㐹搶㠳㌸㠰戹㔷戳敡ち〴ㄶ㘰敥愳搱晤㈰㙡㌵㐴ㅡ㤸〷挰收〴㘶ㄵ㑢㙡〳㜱〱昳㌰攳ㅡ㜹㜴敡㑡戸昸〱㌳㍣ㄷ㌰挳㉣㠵㘷攲挰搵㠸㔴㠶㤷昱〴㙢㝦㤲攴㈹㤲愷㐹㥥〱㔱㔵㌹㠱㜹㤶㌶ㅢ㐹㥥〳㜱〰昳㌷捤慡㌵〸㉣挰扣㐰愳ㄷ㐱搴㌵㄰㘹㘰㕥〲㥢ㄳ㤸戵㉣愹つ挴〵捣慢㡣㙢攴搱愹㙢攱攲〷㑣晦㕣挰散㘹㈹㍣戳㈱慥㐷愴㌲扣㡣昷㤰搴㜸㥦攴〳㤲て㐹㍥〲㔱扢攵〴收㘳摡㝣㐲昲㈹㠸〳㤸㑤㥡㔵㌷㈰戰〰昳㜷ㅡ㝤づ愲㌸扢㐲〳戳ㄹ㙣㑥㘰㙥㘴㐹㙤㈰㉥㘰扥㘰㕣㈳㡦㑥摤〴ㄷ㍦㘰扡攵〲㈶㘸㈹㍣㔳㍣㙥㐱愴㌲扣㡣敦㔸晢㔶㤲敦㐹㝥㈰昹て㠸㉡捡〹捣㑦戴昹㤹攴ㄷ㄰〷㌰慡㡢戰敡㔶〴ㄶ㘰ち㈱㌰扡㠰愸㍦㐱愴㠱㈹〲㥢ㄳ㤸摢㔸㔲ㅢ㠸ぢ㤸慥㜰〹ㅡ㜹㜴敡㜶戸昸〱昳慦ㅦ㜳㥣昹㝥㘵㈹㍣昳㔶搶㈱㔲ㄹ㕥㐶〸㐹㡤敤㐸㝥㐷戲㍤挹づ㈰㙡㌳㕣晤㉦㠶敦㐴㥢㥤㐹㝡㠱㌸㠰改慤㔹㜵㈷〲ぢ㌰扢搲愸て㠸扡ㅢ愲㍤昱挲㈹㌳搸㥣挰摣㐵㡢㌶㄰ㄷ㌰㘵㜰〹ㅡ㜹㜴㙡㍤㕣晣㠰㜹㌳ㄷ㌰㙦㔸㡡散挹㌸挵昷㈱㔲昶つ㐷㤹戰㥡㤹愶攰㤸〰搱ㄳ挶㠱搴散愶晡㜴㙢户㔴摤攲㜴昳搸晡昴攸搶㜴昷ㄴ〸摥㡡㑢㙦戹愳敦㜰ㅡ㤴㥡㔳㙦ㅥ㍢ぢ户摣㜶昷慡㌰㤷㜷搴攲搶㜴戳摣㑢敤敢搵㡦㙥㥥搲㥣ㅥ㕤摦扡愸㈱戶慣扦㡦㕡㙢づ㕥㘰㌶㘱㡡㐹ぢ㘶㥡㙣换愸㜹搱㈲㌳改㔳攳捣收挵㉤〹㜳挲攸摦挲㈴ㄵ愵㙦ちㄷ攰扥愳㔲〵㙡慦摣㤳㌲ㅣ戸敦㠶摥ㄴ攲㕥愵晡㤵㜳ㅣ摡攰㡦㘹扤搸昵ち㤰ㄳ扢㌹㝥ち㡡敦〷㥢㝦昷㜰㑣㜹改〶攳㘰ち㉤搵戲ㅥ搶㥣慡〹㑤慤昵㐹㌳㘸㜱㤳敢㥢㝡㕡㙦愷㉥㑥扢㌴戱愵摢㕢ㅡ摣㑣㥤摡㠴戶㈷㘲㉤挹摦㐲㐷戰㘱昸搱敤㔰〱晣晢㜵㈰敢㌰〵〵㕦昲㜲〴㝦扥㍣㔹㠰㉥㈸㝥〰㡣敦㝤敤捣挷㄰㙦ㅣ戳㠵㑡㘱摦㠳㔰㘷挴㈵攴㈶㥢戱㈶改挰捣㜴㜲戴戹愴愷㔸㤸搸戱㌱㜵扥挱摣摥捤捡昴〶㈳㔵ㄷ㙦㙤㙥㔸㥣㌶㝢㘶摥挹〷摣㐸捤㌰ㅢ㘲㥣昹搵㍤昳㙥㕡㈲㡤戹㜱㤹㜸㥣搵昵摢改づ㄰㈹戲㍡愴愴㐷㠱㍣㍢慥㝢㈳昸搹昹㤵ㅤ㐵㈳㔳昲昳挵㠱㙡搵ㄵ晣戹昹挰〲晢㡤昵㈱㝡㄰攱㍢㍥戵㡢㥦愲敤敤ㄹ㠷晡挸㈶〷慤敥戶㡣戳慡㝡愴攴㜸㠷愹㤳㕣㌵㔱捡㡦㑤〳㤶戴愴敢ㄳ戱㠶㠶㘵㍤㔳ㄳ㥡ㄲつ㡢㤳收愴㔸摣㙣戰㡦搵捤㉤㡤扦㤱㝥ㄵ㜱昷搷扤捡㠳㡢㌵摦㙤〲㤶ㅡ搹ㄳ挹㝥昵攱慤挰ㄸ㠴㈳㥢㝣搵㈲㠶㍥戶㍤㠴㈲晥搷㜳攸㠲㜰晡㕤晢っ㔰㔹㠸㠲㐳㥡㐷挴㘳ㄹ攷ㄸ㘵愶攱挹愷捤㘱㌶愹㜹㔲㌳愶㐸㈶ㅤ愲昱昵㕡昴㥢昹㑣㐹㡢〲㠱挰慦晤㔲〱㔶昸昹搲㥡晦㠰㠳㥤收て攴㔹ㄴ扦㕤ㅥ〱㥦㍤㍢挹㜱昲㈱摦昷㜲〰っ挱戰㤴㐷㉦㝤戲㌰慢㍥摤㘰㜶㑢㠹㕥摥㤷昰攳㐰㌴扢愶㘶㉤挰㑣㥦搱㍤㔲攳㕡敡㤳つ昵㑤㈶㑦㍣㌰㘵㤷㡢㝦㈶㤹昳㌱戹㜴㕡㜳㙢㍤搷戴昵㐸捤㙡㠹㌵戵㉥攲㠴慥挴戲摦戹㌸㘹㔶㜱㙡㘴㝤ㄳ㍥㍣㍡㈷摦㤷愶㘶㉥㘸㍥ㄶ换攲ㄶ㌷㌶㡤㡢㉤㙡晤㑤㌴捡晡㉡〱㐲晡ㄳ㔵愸ちぢ㔵㐹㘱挹慦晤㡥挲ㅥ㡥㤰ㄵ㠸㔷㐸㘲戵敡捦㜸㤷攷戳捡㉥㔹㔳㝢昹㔹㘵㑤慥㈵㕥扥㜳つ㌳㙢ち㜹晣㌵㝥㡦て㘸昷㈱㈰ㄳ挷捤㥥搰㍥㈱晣晦戴㐰慦昸㔱㐴捥昳㌵㈰扢㐵㘶昶改㡥㌰敥愹㜷ㄵ捡戸攷ㄸ搲㜱㜲搹扢㕦㌰㈵㌶摣ㄳ昱捤㐹㜳扥ㅤ㡢戹㠲摤昱挱挷㘱ㄷ㜳㉣㜱扣敤愹ㄹ㥥挲㌵挶ㅡ㕡㉤摤愸收挶挶ㄸ㜷㉤敥㤶㌳㜱捣㌶㑢攴㝣ㅡ㐷ㄲ㈳〵㈲晢㥦㈵㡡㉤㠵㈸戶㔴㐴昸㉡收㡣㜲㜹捦㔸捤昳㘳㉤昵改〵㡤昵㠹ㄲ㌲㥣昵晤㥢搸㈷戱ぢㄵ〱㑣晢㐷㜶㑣㥣㥣㘶捦攷搴㔳㄰搱敥㈱ㄸ㉦㄰㍡戶ㅦ㝢㙥愱㝣㝦慢㕦㌹㕤户㐰㈹㌹搰ㅢ㘱㐴㉢挶㔸ㄶ〲敢㐳攲㌸昱㠲㐴づ㐲敡㌱ㅡ攰㘵㤴挳摣晥㈹摡㠰㜷㜹㘷㔵㜶㠵㐱㜰㔲㜳㉣㌹ㄶぢ〳㥡㕢扡㕡ぢ㑡㑢搰㕡ㅥ㔲㕡㐲㥣㐹㍢ち㔳捥㌱㤵㝤〹捥㝦㕢㑡㈸㤸㠹㌹慡㐵㥣㠳ㅢ搰㍤攴㠷戶愰戸戸㕢㠹㕦慥〹㜶慣晥搶㡣㐳攷㠲摣〹㥥昸㕢愶搷ㅣ挸つ〹〶㜹ち㘱㔴㘰㜳㡣㑡㄰昵ㄷ戰摣㥥㉣㠳〸つ愲㈰挵㑦㐰㤹晤㈹挹㌹敢ㄴづ〵挵㡤㥣つ㕢搲挸捤挱愹㐶〰㜳㘴㌱慢ㄶ㤰〴扡㤵㍣づ扤㔱〵慢攷㌶㙥ㅣ㡥昷〵敡㘹㄰㍢㍦㜷ぢ慢挰㙡收慦〱㔱㉦㐲挸㠱愸戴慤挰ㄸ捡ㄴ敤㠳㄰昵ㄲ㔸づ㐴散ㅦ㐷ㄷ慤ㅥ扥っㄵ㑦愱搹挸㙤㥤㡥愹㔷㘰挷㔳㌲摣㡢㘱〵㙤㜸㘷㥦ㄳ愸㔷挱昰扣㐰晦攴晣收㔲慦挳㠰摦㕥〵扥㐷㑢昵〶㌴㍣㘲ㅡ挳戹㜹㙦攲ㅤて㐴㤹ㅤ昳㐰㐸户扤㘳扥㑤て扣㕣㍢愶㝡〷ㄲㅢ㑣㐷户敢戸㈹㈳㤹敤㕤㝦㠳㔱㌴ㄸ㑤㠳昷㘰挰㡥ㅢ㘳挰㘵㥡昴愱挳捤搱愴戱㜴ㅢ㐷户捦㘱攰㘸搲〴挸㥣㑤摡っ㌶㝦㤳戶挰愲挳㑤晡〷㡣㜵㤳㈶戲㠲㌶戰㤹㈶㝤〱愶㈳㑤晡ㄲ㜶㜹㥡昴ㄵ搴搲愴㐹摣扣㝦㠱㜳㌵㘹ち愴摢㙥搲㌷㜰昳㌶改摦㤰晡㌴㘹ㅡ㌷㘵㍡戳㝤敢㙦㌰㠳〶㌳㘹昰ㅤっ愴㐹戳挰㘵㥡昴㠳挳捤搱愴搹㜴㥢㐳户㉥愸挵搱愴㐳㈰㜳㌶㠹㈷摥昹㥢㔴っ㡢づ㌷㈹〰㘳摤愴㐳㔹㐱ㅢ㤳㔹㘷搷慡㉢㜴ㅤ㘹ㄲ愷㥡收㘹ㄲ㈷愱㑡㤳づ攷收㜵〳攷㙡搲㤱㤰㙥扢㐹㥣戵㡡摦慣㑦㔲㑦㠸㝣㥡㌴㤷㥢㌲㡦搹㑡晤つ㘲㌴㠸搳㠰ㄳ㕤愵㐹〹㜰㤹㈶㜱㉥慢ㅤ搷搱愴㈴摤㑣扡㜱摥愹愳㐹昳㈱㜳㌶㘹㌷愸昳㌷㠹搳㔵㍢摣愴摤㘱慣㥢戴㠰ㄵ戸㥡㔴〶㕤㐷㥡挴㘹慦㜹㥡戴㈷搴搲愴愳戹㜹晤挱戹㥡搴〰改戶㥢戴㌷摣昰㥢搵愴〱㄰搹㘰㔲㙢㝤㜷㌴㜱㔳㥡㤹㡤㔳㙣㝤っㄶ搱攰ㄸㅡ㜰搲慤㌴愹〵㕣愶㐹㥣㔷㙢扢㌹㥡搴㑡㌷晥㡤ぢ挵㌹戰㡥㈶㉤㠱捣搹㈴捥㡥捤摦㈴㑥㥤敤㜰㤳㌸挵㔶㌷改㔸㔶攰㙡ㄲ㘷摥㜶愴㐹㥣㠲㥢愷㐹㥣㥣㉢㑤㕡挶捤ㅢづ捥搵愴攳㈱摤㜶㤳㜸㠲㠱摦慣㈶㡤㠰挸〶㤳㕡慢㐹㈷㜲㔳㑥㘲戶㍡㝦㠳㤳㘹戰㥣〶㥣〰㉣㑤㕡〱㉥搳愴㌱づ㌷㐷㤳㑥愱摢愹㜴㥢〲〳㐷㤳㑥㠷捣搹愴愹㔰攷㙦ㄲ愷昱㜶戸㐹㥣敥慢㥢㜴〶㉢㜰㌵㠹戳㠰㍢搲愴㔹戰换搳㈴㑥ㄴ㤶㈶㥤挵捤攳㡣㘱㔷㤳捥㠶㜴摢㑤攲捣㘲晣㘶㌵㠹搳㡢㝤㥡㜴㉥㌷攵㍣㘶攳搴㘳ㅦ㠳昳㘹昰㐷ㅡ㜰㌲戲㌴㘹㈵戸㑣㤳㌸摦搸㜶㜳㌴改〲扡㕤㐸户昹㌰㜰㌴改㘲挸㥣㑤攲慣攱晣㑤攲㤴攲づ㌷㠹㔳㡦㜵㤳㉥㘱〵慥㈶㉤㠴慥㈳㑤攲搴攴㍣㑤㙡㠲㕡㥡㜴ㄹ㌷慦ㄹ㥣慢㐹㔷㐰扡敤㈶㜱㤶㌳㝥戳㥡挴愹捥㌶㤸搴㕡㥦愴搵摣㤴㉢㤹㡤搳愰㝤っ慥愲挱搵㌴攰搸㕢㥡戴〶㕣愶㐹㥣晢㙣扢㌹㥡戴㤶㙥搷搰㙤㌹っㅣ㑤扡づ㌲㘷㤳㔶㐰㥤扦㐹㥣摥摣攱㈶㜱ㅡ戴㙥搲昵慣挰搵愴搳愰敢㐸㤳捥㠰㕤㥥㈶㥤〹戵㌴改㐶㙥ㅥ㘷㔲扢㥡㜴ㄳ愴摢㙥ㄲ㘷㕣攳㌷慢㐹攷㐰㘴㠳㐹慤搵愴㕢戸㈹户㌲ㅢ愷㘴晢ㄸ摣㐶㠳㍦搱㠰㤳戴愵㐹户㠳换㌴㠹昳戰㙤㌷㐷㤳敥愰摢㍡扡㜱捥戴愳㐹㜷㐱收㙣ㄲ㘷㔳攷㙦ㄲ愷㕡㜷戸㐹㥣㤲慤㥢㜴㌷㉢㜰㌵改㉡攸㍡搲愴㌵戰换搳愴戵㔰㑢㤳敥攱收㕤〳捥搵愴晢㈰摤㜶㤳㌸晢ㅢ扦㔹㑤扡ㅥ㈲ㅢ㑣㙡慤㈶㍤挰㑤㜹㤰搹㙥昰㌷㜸㠸〶て搳攰㐶ㄸ㐸㤳ㅥ〱㤷㘹ㄲ攷㠴摢㜱ㅤ㑤晡㌳摤ㅥ愵ㅢ攷㙦㍢㥡昴ㄸ㘴捥㈶㜱㘶㜷晥㈶慤㠷㐵㠷㥢挴改攱扡㐹ㅢ㔸㠱慢㐹㥣㌵摥㤱㈶㜱晡㜸㥥㈶㜱㘲戹㌴改㜱㙥ㅥ㘷㤸扢㥡昴㈴愴摢㙥ㄲ㘷愲攳㌷慢㐹㡦㐰㘴㠳㐹慤搵愴愷戹㈹捦㌰ㅢ愷慡晢ㄸ晣㤵〶捦搲攰㔱ㄸ㐸㤳㌶㠲换㌴㠹昳搳㙤㌷㐷㤳㥥愳摢昳㜴㝢ㄶ〶㡥㈶扤〰㤹戳㐹㥣㘵㥥扦㐹㥣㠲摥攱㈶㍤て㘳摤愴ㄷ㔹㠱慢㐹㝦㠳慥㈳㑤攲㔴昶㍣㑤攲㈴㜷㘹搲换摣㍣捥㜶㜷㌵改㔵㐸户摤㈴捥㡡挷㙦㔶㤳㌸㌵摥〶㤳㕡慢㐹慦㜳㔳摥㘰㌶㑥㥢昷㌱㜸㤳〶㙦搱㠰ㄳ改愵㐹㙦㠳换㌴㠹㜳攵㙤㌷㐷㤳摥愱摢扢㜴晢ㄸ〶㡥㈶扤て㤹戳㐹㥦㐰㥤扦㐹㥦挲愲挳㑤晡っ挶扡㐹ㅦ戰〲㔷㤳㌸㥢扥㈳㑤攲戴晡㍣㑤摡っ戵㌴改㈳㙥ㅥ㘷摥扢㥡昴㌱愴摢㙥搲ㄷ㜰挳㙦㔶㤳晥〹㤱つ㈶戵㔶㤳㍥攵愶㝣挶㙣㥣挲敦㘳戰㠹〶㝦愷〱㈷昵㑢㤳㍥〷㤷㘹搲㌷づ㌷㐷㤳㌶搳㙤ぢ摤㝥㠲㠱愳㐹㕦㐰收㙣ㄲ㘷摦攷㙦搲㉦戰攸㜰㤳ちち敤㈶晤㤳ㄵ戸㥡愴愰敢㐸㤳㌸挵㍦㑦㤳㡡愰㤶㈶㝤挵捤㘳㍦㕣㑤晡ㅡ搲㙤㌷㠹慢〵戰㕤㔹㑤㉡㠱㜴〳愴㔹ㄷ㘲晦捤㑤昹㤶搹っ㝦㠳敦㘸戰㤵〶㕣㘰㈰㑤晡ㅥ㕣愶㐹㍤ㅣ㙥㡥㈶晤㐰户晦搰㡤昳晤ㅤ㑤晡〹㌲㘷㤳㜶㠶㍡㝦㤳戸㑣愰挳㑤摡〵挶晡㤳昴㌳㉢㜰㌵愹㌷㜴ㅤ㘹ㄲ㤷ㅢ攴㘹ㄲㄷ㈲㐸㤳㌸㔵㐶昵〵攷㙡㔲㈱愴摢㙥㔲ㄹ摣扣㑤敡〷改〶㙦㤳昰〷〶戱㈶㠴搹昶昰㌷〸搰愰㉢つ戸搸㐱㥡㔴〲㉥搳愴扤ㅤ㙥㤰摢㥦㔰晥㔵㑣㈳㐸㌷慥㍤㜰㌴愹㍢㡤ㅣ㔷挱戹㉡㈱㝦㤳戸㘴愱挳㑤攲搲〶摤愴ㅥ慣挰搵㈴慥㜸攸㐸㤳戸昴㈱㑦㤳戸㈸㐲㥡㔴捡捤慢〶攷㙡搲㜶㤰㙥扢㐹戵㜰昳㌶㘹㈸愴ㅢ扣㑤摡㥥㥢戲〳戳㜱㤹㠵㡦挱㡥㌴搸㠹〶㕣㜸㈱㑤摡ㄹ㕣愶㐹㕣㕢㘱扢㐱㙥㌷愹ㄷ摤㜶愱摢㜸ㄸ㌸㥡戴㉢㡤ㅣ㑤㥡〰㜵晥㈶㜱昹㐴㠷㥢挴㘵ㄶ扡㐹㝤㔸㠱慢㐹㕣㝤搱㤱㈶㜱ㄹ㐶㥥㈶㜱㠱㠶㌴愹㉦㌷㡦㉢㌵㕣㑤㉡㠳㜴摢㑤攲㡡づ㙦㤳戸慣㘳㠳户㐹㝢㜰㔳昶㘴㌶㉥昹昰㌱攸㑦㠳扤㘸挰㐵㈰搲愴扤挱㘵㥡挴㜵ㅥ戶ㅢ攴㜶㤳〶搰㙤ㅦ扡挵㘰攰㘸搲㐰ㅡ㌹㥡ㄴ㠷㍡㝦㤳戸㤴愳挳㑤㑡挲㔸㌷㘹㄰㉢㜰㌵挹㠴慥㈳㑤攲㤲㤰㍣㑤㕡〰戵㌴改昷摣扣㝡㜰慥㈶敤〷改戶㥢挴搵㈵摥㈶㜱㠹挹〶㙦㤳捡戹㈹ㄵ捣挶攵㈷㍥〶㤵㌴㠸搰㠰ぢ㔲愴㐹㔱㜰㤹㈶㜱捤㠹敤〶戹摤愴㉡扡㔵搳敤㌸ㄸ㌸㥡㔴㑢㈳㐷㤳戸㜲㈴㝦㤳戸慣愴挳㑤攲昲ㄳ摤愴愱慣挰搵愴㤳愰敢㐸㤳㤶挳㉥㑦㤳㔶㐰㉤㑤ㅡ挶捤㍢〵㥣慢㐹〷㐰扡敤㈶㥤〶㌷㙦㤳㑥㠷㜴㠳户㐹㈳戸㈹㜵捣㜶㠶扦挱㐸ㅡ㡣愲〱ㄷ挷㐸㤳㐶㠳换㌴㠹敢㕦散戸㤰摢㑤ㅡ㐳户戱㜴攳㕡ㄵ㐷㤳挶搳挸搱㈴慥㘲挹摦㈴㉥㜱改㜰㤳戸ㄴ㐶㌷㘹〲㉢㜰㌵改㌲攸㍡搲愴㉢㘰㤷愷㐹慢愰㤶㈶ㅤ挴捤攳㙡ㅡ㔷㤳㈶㐳扡敤㈶㜱搵㡤户㐹㔷㐳扡挱摢愴愹摣㤴㘹捣挶㘵㌹㍥〶搳㘹㌰㠳〶㙢㘱㈰㑤㥡〹㉥搳㈴慥挵戱摤㈰户㥢㌴㡢㙥戳改挶㜵㌳㡥㈶ㅤ㑣㈳㐷㤳戸愲㈶㝦㤳戸摣愶挳㑤攲戲ㅣ摤愴㐳㔸㠱慢㐹㕣慤搳㤱㈶㜱搹㑥㥥㈶㜱㐱㡦㌴改㌰㙥ㅥ㔷昶戸㥡㜴〴愴摢㙥ㄲ㔷〰㜹㥢㜴ㅦ愴ㅢ扣㑤㍡㡡㥢㌲㤷搹戸㐴挸挷㘰ㅥつ㘲㌴㜸〰〶搲愴㌸戸㑣㤳戸㉥挸㜶㠳摣㙥㔲㠲㙥㐹扡㍤〱〳㐷㤳㔲㌴㜲㌴改㐹愸昳㌷㠹㑢㝦㍡摣愴愷㘱慣㥢㌴㥦ㄵ戸㥡昴っ㜴ㅤ㘹ㄲ㤷㄰攵㘹ㄲㄷㄷ㐹㤳敡戹㜹㕣㘵攴㙡搲㐲㐸户摤㈴慥㐶昲㌶㠹㑢㤲㌶㜸㥢搴挸㑤㘹㘲㌶㉥㔷昲㌱㘸愶挱㈲ㅡ㜰〱㤳㌴改ㄸ㜰㤹㈶㜱㡤㤲敤〶戹摤愴ㄶ扡戵搲敤㍤ㄸ㌸㥡戴㤸㐶㡥㈶㜱愵㔱晥㈶㝤〰㡢づ㌷改㐳ㄸ敢㈶㉤㘱〵慥㈶㝤〴㕤㐷㥡挴攵㑣㜹㥡昴〹搴搲愴愵摣扣㑦挱戹㥡㜴ㅣ愴摢㙥搲㈶戸㜹㥢昴㜷㐸㌷㜸㥢㜴〲㌷攵㐴㘶攳搲㈹ㅦ㠳㤳㘸㜰㌲つ戸㤸㑡㥡戴ㅣ㕣愶㐹㕣㉦㘵扢㐱㙥㌷㘹〵摤㑥愱摢㜷㌰㜰㌴改㌴ㅡ㌹㥡挴㔵㑦昹㥢昴㍤㉣㍡摣愴ㅦ㘰慣㥢㜴㍡㉢㜰㌵㠹㉢慡㍡搲㈴㉥慤捡搳愴㥦愱㤶㈶㥤挹捤攳敡㉢㔷㤳晥〰改戶㥢愴㌸捥〷ㄲ敥搹㐲㠵㤰㙥㠰㌴敢㡡挳㌹摣㤴㜳㤹慤㡢扦挱㜹㌴㌸㥦〶㐵㌰㤰㈶晤ㄱ㕣愶㐹㕤ㅤ㙥㤰摢㑤㕡㐹户ぢ攸ㄶ㠲㠱愳㐹ㄷ搱挸搱愴敤愰捥摦愴摦挱愲挳㑤摡ㅥ挶扡㐹ㄷ戳㠲㌶㈶戳㈷愲散〰㕤㐷㥡戴ㄳ散昲㌴㘹㘷愸愵㐹㤷㜲昳㝡㠱㜳㌵改㜲㐸户摤愴摥㜰昳㌶㘹㔷㐸㝤㥡戴㡡㥢戲㥡搹戸愴捣挷攰㑡ㅡ㕣㐵㠳摤㘰㈰㑤扡ㅡ㕣愶㐹㘵づ㌷挸敤㈶慤愱摢㕡㤰攲㠱㌰攸搸敡㈲捥㜶っ㌹㤶㝣㜱㙥㙣敢㜶愹改㡢㘳つ㜸㈶挳㔴慣㍦㐸㔳昴㕢㤸㝣㕡愴㔷㠱㘴晦㈹㘸昷愳ㅡ戰㜰㑡㌶攱昰㈳晢㘲换戲㌱㜰摢㕡摢搶㑡换㕦户㑡㈴㔸㍣昷㍦扦晣搲戱㉣摣㍤扡㉥攱㕦ㅥ㥤㍢户愰㠴㌹搱㈴㉣〷扣ㄶつ攳㥣㜹慥㘳挸㌳ㄱ㍢㙢搱〴愳㙤摦㍥㙤㤴ㄳ㠴〷㌵昰㈹㉥㝥昳㑤摤昳戱慦㐳㐲挵㐹搹戲挳㕥㑦づ挱昸㉡づ㐳扡捤戹扣㜰挰㙡㌰捥敡㥤㤹㕥搶㠰㤹搴㝣换扦戵愹摦㜱敡愸㔶愳扣收㤶㈲㉣㝡换晥㑢扡ㄹ摦㝢ㄱ慡摢づ㔹㝦戹㔸摣愸ㄹ㠲㙡㡡て〷挰㌹晤㔹㜴㍢愶昴攱㑦攰㐶㤴戸挳攴晡㐴㑢㜳㙢㜳㉡㕤㌶ㄳ慢〱捡昸户慣昱㈷㝡挲㜵挵㠷㈲愲㙦㑥㙥㔸㔱ㄳㅦ㍥㈲㙤ち㉥㙣㙡㍥戶㐹慡㈹㙥攵㥦昴ㄶ扣扡㜶㘵ㅡ慥ㄶ㤱㥦㍤〱㕣愸ㅣ㠵昲㈷㔴㘱愱ㅡ戸〹戱昶ㅡ㌵㜲搴㡣戹攵搱㥡慡摡㐸㍣㤶㈸㌷㔳㤱㐸㘵戴㌶㙣搶㐶挳㤱㥡㜰㈲ㄹ慥㡥搶搴㠶㉡㉤ㅦ攳㘶昸㠴㈲㌶㜷ぢ戹愸捤㔱㔷㕡〵㡥㠹〳㤲散扦㐸㐲搵㠸㡣㕦晣摤㜸攴搹㙥搴挸戹敥㐷戳〴晥〴㜱㜷㠸㘵㙥昳っ晣〱敤挰敤㤰昴㠴挴戱㍥㈰㔴㘳㐵㌱敥㠰搲攸㠷㜸㐶ㄹ㠸ㅡち㌹㡦㐸㐱㌵〵搰昳ㄳ挳㕣㐱攳㙥㤸㘱捦㔷晢㠳攵摥㙦慣㠷㐰つ挷㍢㐱晡ㅥ㜲昴攷敢㐰㐸戹㜷慡㠹㜰攷㍥〱㘱㠱挱㐶戳愷㙡㍣㈴散慢扢㉦㜵㔶愸挰〳戰搳敤〸㔷㔶愷慡ㄳ愹㜰㘵㜹搸㡣㤸搱摡㜸㈴㕥ㄱ㑤㔶㔷㠴愳ㄱ戳慡㌶ㄱぢ㡤戴搳㍦〸㥦搰㈸㥢㤳㜶㡣戶㌹敡㑡㌹换戶㜳摡㌱ㄶ㤱昱㕢㘰戰ㅤ〶挱㌷㠸㜷㠸搳㜵㐵摥㐶搱〰㕡散つ愲㌸㘵㔷〳㍣ㅣㄸ戴〳晣㌸捣〸昰㐴攸〵攰㈷㈰㔰㤳挰〹挰㑦㤲愳㍦㕦㔳㈰ㄵ㠰㙢ㄱ挲ぢ㜰戵㉦挰搳慣㔰㠱扦㈲㤴〶戸ㄶ㡦㔱㑡㐵㑤㌳ㅣ慦〸㐷㉡㔲戵㌵昱摡㐴ㅣ慦㠸㔹㔳㤱㡡㈵慢㐲搳敤昴捦挲㈷㌴挳收〴攰㤹㌶㐷㕤改㉣㜰㥤〳昰㙣㐴挶慦〷攰㌹戶晣㐵攴㤷愷摢ㄸ㠳〹捥㈱㤰㙢㠰〷扢〰㝥ㄵ㘶〴昸㔰攸〵攰搷㈰㔰㠷㠳ㄳ㠰㕦㈷㘷〳㝣㈴愴〲昰㍥扥〰敦敤ぢ昰㕣㉢㔴攰㙤㠴搲〰㈷㉢㘲㔱戳挲慣㡣搴㤸攱㐸㔵㈴ㄹ㡦挶㙡㘳搵ㄵ㤱慡摡㜸㜵慣戲㈶ㅣ㥡㘷愷㝦〷㍥愱㤸捤〹挰㜱㥢愳慥㌴〱慥㜳〰㑥㈲㌲㝥㍤〰㜳㥡慣挸㍦㐲㝥㜹昴㡦挱戵㐸㡡㔳㘵㌵挰扢扡〰晥ㄴ㘶〴㜸〱昴〲昰㘷㄰愸愳挱〹挰㥢挸搹〰㌷㐰㉡〰敦散ぢ昰㡥扥〰㌷㔹愱〲㕢㄰㑡〳㥣愸㐹愴戰て㔷㈷慢㈲㠹〸㝥㙢㘲昱㐴㘵戲㉡ㅣ㑢挴㈳ㄵ攱摡㐴㐸愶愷㜲攳晥〱㥦搰㈲扢ㄸ〱昸ㄸ㥢愳慥戴〵㕣攷〰摣㡡挸昸昵〰㥣戶攵㕦㈳扦㍣ㄷ挹愸㈱㐰㑢㈰搷〰〷㕤〰㝦〷㌳〲㝣㉣昴〲昰㔶〸搴㌲㜰〲昰昷攴㙣㠰㡦㠷㔴〰づ昸〲㕣攴ぢ昰㠹㔶愸挰㑦〸愵〱㡥㠷慢㑤散慦攵搵愹㘸㌲ㄲ㑢挵攲㐹ㅣ㠷㤳戵㘶愲㉡㔱ㅢ愹慡愹づ挹搴㔲㙥摣捦昰〹㥤㙣ㄷ㈳〰㉦户㌹敡㑡㔷㠰敢ㅣ㠰㑦㐱㘴晣㝡〰㍥搵㤶ㄷㄵ㐳㜹㈰㉤づ㈰㐰㥣愲慡〱晥晥〷攷㌱戸〴㘶〴昸っ攸〵㘰㍥㈸㑦㥤〵㑥〰づ㤲愳㍦㕦㘷㐳㉡〰晦ㅢ㈱扣挷攰慦㈱昵㝥挹㥤㙢㠵ち昴㐴㈸つ㜰㜹戲㍣㔶㔱ㅥ㐹㐵㉡慢㤲ㄱ㌳㔵ㄱ㑢㔵㔴愵昰㡡㥢㘶㑤㜵㜵㔵㑤㐸愶㠵戲昴㔲昸㠴捥户㡢ㄱ㠰㘵㐶愸慤㉢㕤〹㕤攷〰㝣〱㈲攳搷〳昰㠵戶㝣㐷搴㈶㑦搴㌲㐶ㄳ㥣㡢㈱搷〰㙦㜲〱扣ぢ捣〸昰㈵搰ぢ挰扤㈱㔰㤷㠱ㄳ㠰㜷㈵㐷㝦扥慥㠰㔴〰晥搸ㄷ攰㡦㝣〱㕥㙤㠵ち散㡥㔰搶㌱ㄸ㑦㌲㌱㙢挲昱㐸戲扣㉡㔲ㄵ㌶昱散挰ち㌳ㄵ慦㈹㑦挵㈲戵㘶㙤㌲㈴㔳㍡戹㜱㘵昰〹㕤㘵ㄷ㈳〰换㙣㑥㕢㔷扡〶扡捥〱㜸㉤㈲攳搷〳昰㌵戶㝣㙦搴㈶㡦ㅢ㌳㈶ㄲ㥣敢㈰搷〰扦敥〲㜸㈰捣〸昰昵搰ぢ挰㠳㈰㔰㌷㠲ㄳ㠰〷㤳愳㍦㕦㌷㐱㉡〰扦散ぢ昰㡢扥〰摦㘲㠵ち㠴ㄱ㑡〳㕣㔹㘱㔶㤵㥢㤱㘸愴摣㡣㐵㔲攵ㄵ昱ㅡ㥣㥢㔵挶㜱㘴挶㌷㕣㜵戴㌲㜴慢㥤扥ㅣ㍥愱摢㙣㑥〰㤶㤹㤸摣㜰敡㑡㙦㠷慥㜳〰收晣㑤晣㝡〰㕥㘷换慢㤱㕦㥥挵㘶㑣㈳㌸㜷㐱慥〱㝥搲〵昰晥㌰㈳挰㜷㐳㉦〰て㠳㐰摤〳㑥〰ㅥ㑥㡥晥㝣摤〷愹〰扣挱ㄷ攰㌶㕦㠰ㅦ戰㐲〵敡㄰捡〶戸慡㈲ㅥ慢愸挶晥㥢㡡愴愲搵㌵挹㜸㉣ㅣ㠹㔶㔶㠵昹㑣〳㥣愶㍤㘸愷ㅦ〹㥦搰㐳㌶㈷〰换㉣㑡㙥㌸㜵愵㡦㐰搷㌹〰㜳敥㈵㝥㍤〰㍦㙡换挷㈳扦㍣愸捥㤸㐳㜰ㅥ㠳㕣〳㝣㡦ぢ攰㐹㌰㈳挰ㅢ愰ㄷ㠰㈷㐳愰ㅥ〷㈷〰㑦㈱㐷㝦扥㥥㠴㔴〰扥搳ㄷ攰㍢㝣〱㝥摡ちㄵ㤸㠱㔰ㅡ攰㜸㔵㜵戸㈲ㄵつ㔷攰㈹㔶搸㡦愳搸㡤㙢㉢慡㙢挲攱愴ㄹ慦㡡㐷㙢㐲㌲つ㤲ㅢ㌷ㄳ㍥愱扦摡挵〸挰捦摡ㅣ㜵愵ㅢ挱㜵づ挰㥣㌷㠹㕦て挰捦摢昲㐳㤱㕦㥥攲㘷ㅣ㐱㜰㕥㠰㕣〳㝣扤ぢ攰㈳㘱㐶㠰㕦㠴㕥〰㍥ち〲昵㌲㌸〱㜸㉥㌹晡昳昵㉡愴〲昰㕡㕦㠰慦昶〵昸㜵㉢㔴㈰㠱㔰ㅡ㘰㈰㔹㤵㡡㐴㙢㜰ㄶ㘱㐶捡挳㌸㉢㉥㡦攲ぢづ〳戹㐴㙤㔵扣㈶ㄵ㝡挳㑥㥦㠴㑦攸㑤㥢ㄳ㠰摦戲㌹敡㑡摦〶搷㌹〰㜳捥㈳㝥㍤〰扦㙢换㡦㐶㝥㈳㐱㡢㌸挱㜹ㅦ㜲つ昰㐵㉥㠰昹っ㕥〲晣〱昴〲㜰㌳〴敡㈳㜰〲昰㈲㜲昴攷敢㘳㐸〵攰㍦晡〲㝣㥥㉦挰㥦㕡愱〲㘹㠴戲づㄱ搱㐴㑤㉣㕡㔳㘹㔶搵㐴㈲戵戵搱摡ㄴ㑥㈹㤲攱㥡㘸㌵捥摦昰㍥㈴搳て㔹晡㘲昸㠴㌶搹挵〸挰㌲昳搰搶㤵㝥づ㕤攷〰扣ㄹ㤱昱敢〱㜸㡢㉤㍦ㅥ戵挹昳ㅦ㡤〵〴攷ぢ挸㌵挰愷戸〰㍥ㄹ㘶〴㤸戳て〵攰攵㄰愸慦挰〹挰㉢挸搱㥦慦慦㈱ㄵ㠰㑦昲〵昸〴㕦㠰晦㙤㠵ち㥣㡥㔰ㅡ攰㔴慣㉡㡡㔷挲慣㐹搵㐴昰ㅤ㔷㕢㙥搶挶㔳㌵攵㘶㔵扣㌲ㄶ慦㌴㐳摦摡改捦㠰㑦攸㍢㥢ㄳ㠰户摡ㅣ㜵愵摦㠳敢ㅣ㠰㝦㐰㘴晣㝡〰晥㡦㉤㍦ㄷ昹攵攱㤸㐶ㄳ挱昹〹㜲つ昰㌱㉥㠰㔷挲㡣〰㜳收愰〰㝣〱〴昲〷戱〴攰ぢ㠵戳〰㉥挴愹扤〰摣攸ぢ昰㐲㕦㠰㡢攰挴㔰㠱㑢ㄱ㑡〳㕣㡢㉢㄰戵戱ち㡣㤳挳戵ㄱㅣㄹ㠰㜲㙤㘵㌴㤶㡡攲摣愲㉡ㅡ㑢㠶㡡㉤ㅦ攳㌲昸㠴〲㌶㈷〰㜷戵㌹敡㑡㑢挰㜵づ挰〶㈲晢〱ㅣ戴攵㔷㈱扦㍣㌹搴㐸ㄳ攰敥㤰㙢㠰攷戹〰扥〶㘶〴戸〷昴〲昰戵㄰愸㔲㜰〲昰㜵攴攸捦搷㜶㤰ち挰㐷昸〲㝣㤸㉦挰摢㕢愱〲晦㠳㔰搶㌱㌸㠹〳㐱慡㌲㕥㔵㕢㠵敢ㄱ戸搶㤳㠸㈵㉡㙢㉢㙢㔳㤱昲㜸㉤㐶搰愱ㅤ散昴㌷挱㈷戴愳捤〹挰㍢搹ㅣ㜵愵㍢㠳敢ㅣ㠰㝢㈱戲ㅦ挰㥣昶㈷昲摢㤱㕦ㅥ慢㙡ㅣ㐷㜰㌸昵㑦〳㍣搵〵昰㕤㌰㈳挰㝤愰ㄷ㠰敦㠶㐰昵〵㈷〰慦㈷㘷〳㕣〶愹〰㝣㤰㉦挰ㄳ㝣〱摥挳ちㄵ戸ㅦ愱㉣㠰㈳ㄸ㕢㐴㙢ㄲ㤱摡㘴㌲㔲㤳愸㠸㐷换㈳搵㤵攱㡡㜸㈴㔵㘹攲ち㘶㐸愶摢㈱慢昱〰㝣㐲晤敤㘲〴攰扤㙣㡥扡搲扤挱㜵づ挰〳㄰搹て攰㝤㙣昹愳挸㙦慣㘰㤵换〹搰㐰挸㌵挰〷戸〰晥ぢ捣〸昰㈰攸〵攰挷㈱㔰扦〷㈷〰㍦㐱㡥晥㝣敤〷愹〰㍣搴ㄷ攰ㅡ㕦㠰换慤㔰㠱㘷㄰㑡〳㕣ㄳ㡥㔶㐴㘳攵攵㔵攵㤵挹㐸㘵㌹㥥〲㥦㑣挵㔳㔵昱慡㔸戴戶㌶㔲㔱ㅤ㤲愹㜲挸㘸晣ㄵ㍥愱㑡扢ㄸ〱㌸㘲㜳搴㤵㐶挱㜵づ挰㔵㠸散〷㜰戵㉤㝦〱昹攵㠱扣挶ㄹ〴㠷㔳敥㌴挰扦㜷〱晣ち捣〸昰㔰攸〵攰㔷㈱㔰挳挰〹挰慦㤱戳〱㍥〰㔲〱㜸㕦㕦㠰〷昸〲㍣挲ちㄵ㜸ぢ愱㌴挰㔵ㄱっ㤳愳挹㜰摣㑣㐶㈳㘱㕣㝣挰搵㠸㘸㌸ㅣ挶攸㌹ㄹ㉤㌷㤳㈱㤹收㐶㠰摦㠶㑦㘸愴㕤㡣〰㉣㌳摣㙣㕤改㘸攸㍡〷攰㌱㠸散〷昰㔸㕢晥㈱㙡㤳愷ㄵㅢ攷ㄲ愰昱㤰㙢㠰晢戸〰晥〴㘶〴㜸〲昴〲昰愷㄰愸㠳挰〹挰㥦㤱戳〱㥥っ愹〰摣换ㄷ攰㥤㝣〱㥥㙡㠵ち㙣㐶㈸つ㜰慡㈶㕥㕥㔹㔵㔹ㄳ慦慥挵昷ㅢ捥ㅦ㉡㉢㜱㈲㕣㔹㠵〳㜱㉣㤱挰㔹㠴㑣㔱㈳㠸㕢攰ㄳ㥡㙥ㄷ㈳〰换散㌴㕢㔷㍡ㄳ扡捥〱㜸ㄶ㈲晢〱㍣摢㤶晦ぢ戵挹愳㥣㡤ぢ〹搰挱㤰㙢㠰扢戹〰晥ㄶ㘶〴昸㄰攸〵攰敦㈰㔰㠷㠱ㄳ㠰户㤲戳〱㍥〲㔲〱戸慢㉦挰挵扥〰ㅦ㘵㠵ち晣㠸㔰ㅡ攰㔸慡㌶㕥㤱愸慣㌱ㄳ㌸〶㔷㈵换㜱㍤戸愲㈲㔶㤱㑣㔴㠶换ㄳㄵ搵㘶㐸愶㤷ㄱ挴㥦攰ㄳ㥡㘷ㄷ㈳〰换捣㌲㕢㔷ㅡ㠷慥㜳〰收㝣㌴㍦㠰㤳戶扣ぢ敥ㅡ捡㜳慥㡤换〹㔰ち㜲つ昰て摦㍢㉦㔷㜶㠵ㄹ〱㥥て扤〰㕣〲㠱慡〷㈷〰ㅢ攴㙣㠰ㄷ㐲㉡〰㝦㡢㄰摥换㤵摦㐰敡扤㕣搹㘸㠵ち昴㐰㈸つ戰ㄹ慤愸慥慥慣愸㈸㉦慦㌰㈳㈹戳〲㐸㔷攰㉡㑦㌲㕣㕢㔱㔳㥤愸㉥て挹搴㌰㠲搸ㄳ㍥愱㘶扢ㄸ〱㔸㘶㠵搹扡搲㘳愰敢ㅣ㠰㌹㤷捣て攰㔶㕢扥〳㙡㤳㠷㠰ㅢ㔷ㄳ愰挵㤰㙢㠰晦敥〲戸ㄷ捣〸昰ㄲ攸〵攰㕤㈰㔰㑢挱〹挰扤挹搹〰ㅦ〷愹〰晣㠹㉦挰晦捦ㄷ攰ㄳ慣㔰㠱扥〸㘵ㅤ㈲㌰㌰慥愸挴㉥ㅣ挵つ㡤㥡捡昲摡㕡戳摡慣慡慣㡣㐶㉡㈲挹㔸㘵㌴㈴搳扡〸攲敥昰〹㥤㘴ㄷ㈳〰换㡣㉥㕢㔷扡ㅣ扡捥〱㤸昳挰晣〰㍥挵㤶敦㠵摡㡣ㅢ㔸挹昵〴攸㌴挸㌵挰㙦戸〰摥ㄷ㘶〴昸㜴攸〵攰㠱㄰愸㌳挱〹挰㠳挸搱㥦慦㍦㐰㉡〰扦攲ぢ昰㑢扥〰㥦㘳㠵ち散㠷㔰ㅡ攰捡㔸㉡ㄵ㐹㠴慢㙡昱ㄳ愹㡣㤴挷捣㜸㈲㤱㡣㈴㙢慡㜱㈱㍥㔵㕢ㅢ㍡搷㑥ㅦ㠶㑦攸㍣㥢ㄳ㠰㘵㌶ㄶ㌷㡢扡搲㍦㐲搷㌹〰㜳づ㤷ㅦ挰ㄷ搸昲㉡攴㤷挷挷ㅢ户㄰㥣㡢㈰搷〰㍦攵〲㜸㈸捣〸昰挵搰ぢ挰晢㐳愰㉥〵㈷〰て㈳㘷〳㝣㌹愴〲昰㕦㝣〱㝥捣ㄷ攰㔵㔶愸挰〸㠴搲〰㔷挷捡㙢愲㤵昱㜸㌸㤲愸㠸㔴㈴㜱〴づ㈷㉡㉢㤳㘶㙤ㄵづㄲ㌱〰㉣搳愹〸㘲ㅤ㝣㐲㔷摡挵〸挰㌲㤳捡搶㤵㕥つ㕤攷〰捣昹㔷㝥〰慦戵攵攳㔰㥢挱㍦㉡㙥昰捦㤶慢㙢敤㉡㈷㐲㑥㐷扥㤴㑣捦愱㑤㌹㔹敢㈷㜴㍤㙣昱㡢㘷戳挰戶㐷㤷攲㥢挱昸晥㡤㔳㍤㜳㘳㈶晥㜲㥤㌹㘴搴挸敡㈱㘳㤶㈶捣〶晥㉤㔹㑣摢㠰㙢挱㡥㡤ㄳ㕡昱ㄶて㜴㥥搵㕣㈷㝦攵㤴㔳㜷戶戳㘷㜶っ戲ㅦ㈶扤㔷扢挴晥㐳挲戶摢搴㤶㡣ㅦ㥥㡤㡣〹㑤㔰っ攲愳愷㜷㙣攷ㅣ㑦㐵摥戵㕤㡡扦ㄸ㡤扦㘵㙢㈶敤㠸慤㤸捤㔷㔴搸㐵つ昴晢㑢搸搶㤳㝦昱戰㕤㍢挰㤸愶挵㡤扢㘳ㅢ㜶昵昹戳㜹㈳敢搳㌲捤愹て昴捡戸〹昰〴愶㘰㝢㡢㠷昷ㅦ搵扦扡昸㑥散㘸晦㡢㈴摣㝦摢攷ㄵ㌱㈵㝦㠲挶㌴㐴㔴摣愷ㄸ㡦㈲㜵〷㤸晥㜸㤳晤扣摢摢㘰昰㌶晥昸扢攷㐱挰户㕡ち捦㠳㠰敦㐶㈴昹〰捤㐱㤲捣摥戰摥㤶扡昶㠶㝢㈰挵㙦㠱㜱〸㙣㝢㜴㔱て㠲攱ㅥ愱っ捥㜴〹ㅣ愶㌷扣慥㝦㤵扡〱改散㘲㠳挶ㄱ慣扦つ㈶晤㝤㑡㕥㥢慢攴㌵㤶挲昳㠸摥挷㤹㤲㤱攲捥㤲㥦戰愵慥㤲㥦㠴ㄴ扦㤸㌴慦㑢㝥ㄶ㡣㉥昹慦㜸ㄷ攰扥㠹㕥㡤敥㕦慤慥㜰㤵扣㠰㈵扦〸㤳晥㍥㈵㕦㥣慢攴㡢㉣㠵攷攱戹慦㈲㤲㤴摣攴㉣昹㌵㕢敡㉡昹㜵㐸昱㡢㤹攷扡攴㜷挰攸㤲㌹ㅢ㈳搰愲㑢ㅥ〵㤴捦㜳㤵㥣㘶挹ㅦ挱愴扦㑦挹㘷攵㉡昹㑣㑢攱㜹慣敤愷㠸㈴㈵ㅦ攷㉣昹㌳㕢敡㉡㜹ㄳ愴昸挵愳㜹㜴挹晦〰愳㑢收晣㠶挰㐹扡攴㜱㐰㜹㠵慢攴攵㉣昹㙢㤸昴昷㈹昹㠴㕣㈵ㅦ㙦㈹ㅡぢ㐶㡣ㄸ昴摤㤶愹㤷㙦㍡戵晥愵昵换搲敡㍢㐴㤲㤲捦㜰㤶扣搵㤶扡㑡收ㄴ〳晣攲愱㤸扡攴㥦挱攸㤲㌹㘳㈰㜰戶㉥戹慥㝦㡤㕡散㉡昹㕣㤶捣㥢昰晤㝤㑡㕥㤴慢攴㘶㑢攱㜹ㄴ㉣敦搳㑢挹ㄷ㍡㑢㤶㥢昵㡣敦㉡㌹〸㕢㈹昹㘲㕤㌲敦愲敢㤲㜹て㍥㜰愹㉥㜹㌴㜶㡣㝡㔷挹㤷戳㘴摥搶昶㉢㌹㤹慢攴㠴愵昰㍣愴㤵㜷扥愵攴慢㥤㈵换敤㙦㑦挹扣つ㉥㈵慦搵㈵昳扥戴㉥㤹㜷戵〳搷敡㤲挷愱攴㈳㕤㈵㕦捦㤲㜹愳搸慦攴㐳㜲㤵㝣戰愵昰㍣㍥㜵㈰㈲㐹挹户㌸㑢㤶ㅢ捡㥥㤲〷挳㔶㑡扥㑤㤷捣扢戹扡㘴摥㈷づ摣慥㑢ㅥ搳㍦慡愶扢㑡㕥挷㤲㜹敢搵慦攴㐹戹㑡㍥挸㔲㜸ㅥ㙣捡扢戳㔲昲扤捥㤲攵ㄶ慤愷㘴摥慡㤵㤲敦搷㈵昳晥愸㉥㤹㜷㕥〳て敡㤲敢昰昱ㅢ攳㉡昹㘱㤶捣㥢㤹㝥㈵㡦挸㔵昲㠱㤶挲昳挸搱㐹㠸㈴㈵㙦㜰㤶㉣㌷㍤㍤㈵昳收愷㤴晣戸㉥㤹㜷ㅣ㜵挹扣㤷ㄹ㜸㔲㤷㍣ㄶㅦ扦㕡㔷挹㑦戳㘴摥ㅥ昴㉢㌹㤲慢攴㑡㑢攱㜹ㄸ㈸敦㈰㑡挹捦㍢㑢㤶摢㠸㥥㤲㜹㍢㔱㑡㝥㐱㤷捣㝢㜸扡㘴摥ㅤっ扣愴㑢ㅥ㠵㤲㝦敦㉡昹ㄵ㤶㝣㌴㑣晣㑡摥㈷㔷挹〳㉣㠵攷㌱㥤扣㈷㈷㈵扦攵㉣㔹㙥捣㜹㑡收つ㍡㈹昹ㅤ㕤㌲敦㤸改㤲㜹扦㉤昰㥥㉥㜹㉣㜶㡣㝥慥㤲㍦㘰挹扣㠵攵㔷㜲㥦㕣㈵敦㙡㈹㍣て搰攴㕤㉥㈹昹㔳㘷挹㜲慢换㔳㌲㙦㜹㐹挹㥢㜴挹扣捦愴㑢收ㅤ慣挰攷扡攴㌱㐰㜹㐷㔷挹㕢㔸昲戹㌰昱㉢㌹㤴慢攴㔲㑢攱㜹戴㈵敦ㅢ㐹挹晦㜲㤶慣㙦ㅥ㘵ㅦ㤷㜹ㄳ㐹㑡晥㐶㤷捣㍢㌷扡㘴摥ㄳち㝣慢㑢ㅥ㠹㠳㥣攱㉡㜹㉢㑢收㙤ㄶ扦㤲㡢㜲㤵摣挵㔲㜸ㅥ㍡挹㍢㌱㔲昲捦捥㤲攵㜶㡣〷㘵摥㤶㤱㤲ぢ戰ㄲ〳㘷㜲扣ㄷ愲㑢收㕤㤶㐰㈱愴㌸㉤ㅡ〹㤴㝦摡敡㍣㤳㉢㠲㐲昱挶㠵㕦挹㕢㘱敡㝢昲昹㥤愵昰㍣づ㤲昷㌶愴攴㈰攲㘶㑥㍥攵〶㠷愷㘴摥攸㤰㤲扢敢㤲㜹㜷㐱㤷捣晢ㄶ㠱㥥扡攴㌱㐰昹㉢㔷挹㈱㤶捣㕢〱㝥㈵㙦挹㔵昲㘶㑢攱㜹㔰㈳敦ㄶ㐸挹㍢㌹㑢㤶㕢〶㥥㤲㜹敢㐰㑡敥愵㑢收昵㝡㕤㌲敦〴〴㝡敢㤲挷〱攵㑦㕣㈵昷㘱挹扣戸敥㔷昲〷戹㑡㝥摦㔲㜸ㅥ愱挸敢敦㔲昲ㅥ捥㤲攵㈲扣愷㘴㕥㡣㤷㤲晢敢㤲㜹㜵㕣㤷捣㙢敢㠱扤敤㤲愳敡㑤㔷挹晢戰㘴㕥慥昶㉢昹㤵㕣㈵扦㙣㈹㍣て㌷攴ㄵ㙤㈹㜹㠸戳㘴戹慣敤㈹㤹㤷户愵攴戰㉥㜹ぢ㜸㕤㌲慦㔶〷㉡㜴挹㘳㜰㤰㝢捥㔵㜲㠴㈵昳〲戰㕦挹㑦攷㉡昹㈹㑢攱㜹散㈰慦ㄱ㑢挹㐳㥤㈵换㠵㘲㑦挹扣㘰㉣㈵て搳㈵昳ち慥㉥㤹搷㝦〳〷攸㤲挷㘲㕦㝥捣㔵昲〸㤶捣㑢慡㝥㈵㍦㥣慢攴㠷㉣㠵攷㠱㠰扣敡㉡㈵㡦㜵㤶㕣㘲㑢㕤㈷㥦扣〴㉢㈵㡦搷㈵昷〴慦㑢收ㄵ搵挰㐴㕤昲㘸㥣ㄶ摤攳㉡㜹ㄲ㑢摥〱㈶㝥㈵慦换㔵昲ㅤ㤶挲昳愸扥㕥㠸㈴㈵捦㜰㤶㉣ㄷ㌳㍤㈸昷㠶慤㤴㍣㑢㤷捣慢㡣扡攴扥㜸ㄷ㤸㘳㤷㕣愳㙥㜶㤵㝣〸㑢收㘵㍦扦㤲慦捦㔵昲㜵㤶挲昳㄰㍤㕥ㄹ㤴㤲㡦㜲㤶㍣搰㤶扡㔰收㘵㐲㈹㜹㥥㉥㌹っ㕥㤷捣慢㝥㠱戸㉥㜹㈴昶攵慢㕣㈵㈷㔹㜲ㄵ㑣晣㑡扥㍣㔷挹㤷㔹ち捦攳敤㠶㈲㤲㤴㝣戴戳㘴戹攰收㐱㜹ㄸ㙣愵攴〶㕤㌲慦㠴改㤲㜹ㅤ㉤搰愴㑢ㅥ㡢ㅤ攳〲㔷挹㡢㔸㌲㉦㑤昹㤵㝣㙥慥㤲捦戱ㄴ搹て㥥ぢ㑤戴换㔸㠲戸挶戱㈴㑢㐱㠲挵扣㜲攵㝢つ㐶㥥〴㌳㐴㍦㌲〳慢戴捣㔶ㄱ㤴㘲〳㡢㔳扣㌸搵㉤挵挵㕢愶㍣户㐳㥥㌶搶㌰㡡㉢换扡攳改ㄹ㉤ぢ捤㤶㐹㜸ㄸっ㥥㤹㌱戳扥搱㕡戵㠴㠷挴昰㈹〶昶昳ㄹっ攱戸㉡㌰㤰㥡摡㠲〷㌶㜴㑤㑤㘸挵㈳㘷㤲㈵㡤搳㘲改戴搹搲昴㕢㔸摤㠸愹㌰晣〳㘵昸搱て搵昰㕤愱挶愵㘷搹捦㜳㜰㍣㔷愷ㅤて晢戹㑡㠵㝣攸挶慦㕢摢㈸㡢㙤ぢ搵ㄹ攸戳摣挵搹㕣戱㡢㕣昲挲㠳㍣㌰㕢㠲ㅤ㔵㔲㉦ㅥ㈹㘷㥣挰㉥户愱㌸㈱〵㐵搳搰敡㝣ㄷ改㜸㠶搱戵㜱㙥慣愵㈵戶慣愴㜱㙥㠳搹㌴㍦扤愰㘴敥ㄲ㕣㤵挴〳㝣㄰慣愴愴挴㌸〹晦㌳〳㕦愱㌹昶㕥㜵㌲㔳㉤㈷㔹〱ㄲ㔴㠷㐰挱㍤换㉡昷㐴摦㜲㑦ㄳ搳㑣戹愷搳扤つ㘱㜵戹敡〸昸戳㘴攳㑣㈸㌲㈹㜹㔱㑢㍥㑦㘷搱晣て㈴㘷㠳〴ㄵ慦㘰㌹㔲愶㝤㔳㥥㈷愶㤹㤴攷搳摤㤱㜲㠱㥤㜲㈵ㄴ㤹㤴扣㈸㈵㈹㉦愰昹㠵㈴ㄷ㠱〴搵㈲㜷捡㠵扥㈹㉦ㄵ搳㑣捡换攸敥㐸㤹戶㔳㕥〱㐵㈶攵㜱㜶捡㔵㌴㕦㑤㜲㈵㐸㔰㥤攰㑥ㄹ昷㑤戹㐶㑣㌳㈹搷搲摤㤱㤲㤷㤵〴搸㙢愱挸愴攴㐵㈱搹捡敢㘸㝥㍤挹つ㈰㐱㜵㤶㍢攵愱扥㈹㙦ㄲ搳㑣捡㥢改敥㐸㜹慥㥤昲㔶㈸㌲㈹㜹㔱㐷㔲摥㐶昳㍦㤱摣づㄲ㔴ㄷ扢㔳㑥昳㑤㜹愷㤸㘶㔲摥㐵㜷㐷捡换敤㤴敢愱挸愴攴㐵ㄹ㐹㜹て捤敦㈵戹て㈴愸㜸〵挶戱晢㡣昳㑤昹愰㤸㘶㔲㍥㐴㜷㐷㑡㕥㤶ㄱ㘰ㅦ㠱㈲㤳㤲ㄷ㔵㈴攵㥦㘹晥愸昸㠰〴搵㙤敥㤴〷昸愶晣㡢㤸㘶㔲㍥㉥敥〵㔶摥〲戵捥㑥昹㈴ㄴ㤹㤴扣㈸㈲㈹㥦愲昹搳㈴捦㠰〴搵晤敥㤴㔱摦㤴ㅢ挵㌴㤳昲㌹扡㍢戶昲㘱㍢攵摦愰挸愴攴㐵つ㐹昹〲捤㕦㈴㜹〹㈴愸㜸〵挳〱散㘰摦㤴慦㡡㘹㈶攵㙢㜴㜷愴㝣摡㑥昹〶ㄴ㤹㤴扣㈸㈱㈹摦愴昹㕢㈴㙦㠳〴搵ぢ敥㤴㝢晡愶㝣㑦㑣㌳㈹摦愷扢㈳攵㉢㜶捡て愱挸愴攴㐵〵㐹昹ㄱ捤晦ㅦ挹挷㈰㐱昵㡥㍢㘵㙦摦㤴㥦㠹㘹㈶攵㈶扡㍢㔲昲戲㠲散㍥㥦㐳㤱㐹挹㡢〲㤲㜲㌳捤户㤰晣〳㈴愸㌶戹㔳㙥攷㥢昲㑢㌱捤愴晣㡡敥㡥㤴㕢散㤴㕦㐳㤱㐹挹㐱扤愴晣㠶收晦㈶昹ㄶ㈴愸扥㜱愷㉣昱㑤昹扤㤸㘶㔲晥㐰㜷㐷捡慤㜶捡ㅦ愱挸愴攴愰㕣㔲晥㐴昳㥦㐹㝥〱挱昳㐸㐰ㅤ扢捦㉦摦昹㝤昱ㄵ㤶搰㌴㤳戲ぢ㔸㘷捡㈲挴㄰㘰㡢愱挸愴っ㐲㉡㈹〳㌴敦㑡㔲〲ㄲ㔴摤摤㈹扦昵㑤搹㑤㑣㌳㈹扢搳摤戱㤵㈱㍢㘵㑦㈸㌲㈹㜷戲㔳㤶搲㍣㐴戲ㅤ㐸㔰㜱〴散搸捡㝦昸愶摣㐱㑣㌳㈹㜷愴扢㈳㘵ㅦ㍢攵捥㔰㘴㔲㜲㔰㉢㕢搹㡢收扢㤰昴〶〹慡晥敥㤴ㅦ晢愶摣㑤㑣㌳㈹晢搲摤㤱㜲ㅦ㍢㘵ㄹㄴ㤹㤴㐳散㤴晤㘸扥〷挹㥥㈰㐱ㄵ㜶愷㝣摢㌷攵摥㘲㥡㐹㌹㠰敥㡥㤴ㅣ㤶㑡㉦昷㠵㈲㤳㜲愸㥤㜲㈰捤〷㤱っ〶〹慡㘱敥㤴㉦昹愶摣㑦㑣㌳㈹挳㜴㜷愴ㅣ㘱愷慣㠰㈲㤳㤲㠳㐲〱戶㤲收ㄱ㤲㈸㐸㔰㡤㜷愷㝣挶㌷㘵㡤㤸㘶㔲搶搲摤㤱㜲㤲㥤㜲㝦㈸㌲㈹㌹愸㤳㤴挳㘸㍥㥣攴〰㤰愰攲〸捥戱晢戴昹愶慣ㄳ搳㑣捡㤱㜴㜷愴攴戰㑥㠰ㅤつ㐵㈶攵㔱㜶捡㌱㌴ㅦ㑢㌲づ㈴愸收戹㔳摥攷㥢㜲愲㤸㘶㔲ㅥ㐴㜷㐷捡愴㥤㜲㌲ㄴ㤹㤴ㅣ㔴挹㔶㑥愱昹㔴㤲㘹㈰㐱搵攰㑥㜹扢㙦捡㤹㘲㥡㐹㌹㡢敥㡥㤴㡢散㤴㜳愰戰㔳ㄶ㉦㠱㜴㝦扦扢摤㝡㄰攴昸㜳ち㠳昰ㄷ㍦昰㔴㑢㌳㠹㜱捣㈲摣㌵㕦㌶愶㈹摤戲㡣㠱扡攰㌹㜳挵㜲㑦扣愸㜰攸慦㡢挵搱搰㙥〸挵㔷昱捤搸扣晦㐳ㅣ㡥㑦摢㙦㤶㌳攲㌰扣㑡ち〳㡡㠳㍦㙥戰扡〹ㄹ㤸㘵戸㈸㤴攲㠰㔰ㄴ晦㘳㈹づ㠴挲㌸っ㐰ㄵ㜳㘴搱攱㈱づ㔳晦捡扦㠲㜲㌸㤲愹ㄳ㔸ㅣ㔳ㅦ㐱づ㙦昸㉡㍤挹㤲㤶㜰㤸愲㑥戶㙢扤捥慡搵摥扡攵戶攲摡慣慤攳挰㐴戶敥ㅡ攷搶捤㘳㡡搳愰攲ㄶㅡ㌱㜲ㅣ㠷㐸晡戸㌳㍤〷㈱㤴敡昴㘷㠱㤳㘰㔷㘵愵攷㠰㐴ㄴ㔷㘶愵攷㈰㐵ㄴ慢㥤改㔳㑣挱㐱㠹愴㥦㑦㡥㘳ㄲ㐹扦挰㤹㝥愵㈵搵改㌹㄰㤱㘰㤷㘵愵攷攰㐴ㄴ㤷㘶愵攷㠰㐵ㄴ㤷㌸搳㌷㌰挵愵㔰㐹晡㐶㜲ㅣ㥦㐸晡㈶㘷㝡づ㑥摡户㝥㤵ㅤ散㠲慣昴慢㙤挵捡慣昴㔷摡㡡㍦㍡搳户㌰挵ㅡ愸㈴㝤㉢戹戵攰㈴㝤摡㤹㥥〳㤵昶昴ㅣ愰挸戶㥣㤳㤵晥㝡㕢㜱㜶㔶㝡づ㘴挴攳て捥昴㑢㤹攲㈶愸㈴晤㌲㜲ㅣ户㐸晡攳㥣改㌹㘸㘹㑦㝦㥢ㅤ散昴慣昴ㅣ挰㐸㤶搳戲搲㜳㔰㈳㡡㔳㥤改㑦㘲ちづ㘲㈴晤挹攴㌸㠶㤱昴换㥤改㌹㠰㘹㑦捦㠱㡢〴㍢㌹㉢晤扤戶攲愴慣昴ㅣ攰㠸挷㠹捥昴愷㌱挵㠳㔰㐹晡搳挹㍤〴㑥搲㥦攱㑣捦挱㑣㝢晡㍦摢挱㤶㘵愵㝦搴㔶㉣捤㑡摦㘶㉢㡥㜵愶㍦㥢㈹㌸戸㤱昴攷㤰㝢ㅣ㥣愴㍦搷㤹㥥〳㥢昶昴ㅣ搰挸戶戴㘶愵㝦摡㔶戴㘴愵攷挰㐷㍣㡥㜱愶㕦挹ㄴㅢ愱㤲昴ㄷ㤰攳㌸㐷搲㕦攸㑣捦㐱㑥㝢晡ㄷ散㘰㡤㔹改㌹攰㤱㉣つ㔹改㌹〸ㄲ挵㐲㘷晡㑢㤹㠲㠳ㅥ㐹㝦ㄹ戹搷挰㐹晡换㥤改㌹攰㘹㑦捦㠱㡥〴㥢㥦㤵晥㉤㕢㤱捡㑡晦戶慤㌰㥤改慦㘴㡡昷愰㤲昴㔷㤱㝢ㅦ㥣愴扦摡㤹㥥㠳㥦昶昴ㅣ昴㐸晡㔸㔶㝡づ㠴㐴㌱㉦㉢晤挷戶㘲慥㌳晤戵㑣挱挱㤰愴扦㡥摣㈶㜰㤲晥㝡㘷㝡づ㠴摡搳㜳〰㈴㔹づ捦㑡扦挵㔶ㅣ㤶㤵㥥〳㈵昱㌸搴㤹晥㈶愶昸ㄲ㉡㐹㝦㌳㌹㡥㡢㈴晤㉤捥昴ㅣㄴ戵愷攷㘰㐸㠲捤捥㑡捦〱㤲㈸㘶㘵愵晦搶㔶捣㜴愶扦㥤㈹㌸㐸㤲昴㜷㤰晢〱㥣愴㕦攷㑣晦愳㈵搵挷㝣づ㡣㈴换搴慣昴㍦摢㡡㈹㔹改㝦戱ㄵ㤳㥤改搷㌳㐵㈱㠸愴扦㠷ㅣ挷㑢㤲晥㕥敢つ㤹㔲づ㤶摡户㍥〰㑥搲㑦挸㑡捦㠱㤳㈸挶㘷愵攷㘰㑡ㄴ攳㥣改ㅦ㘴㔴づ㥥㈴晤㐳攴㌸㜶㤲昴て㕢㙦㈴㍤〷㑥敤改㌹㘰㤲㘰愳戲搲㠷㙣挵挸慣昴ㅣ㔸㠹㐷㥤㌳㝤ㅢ愳敥〰㈲改ㅦ㈳挷㜱㤴愴摦㘰扤㤱昴ㅣ㐴戵愷攷攰㐹㠲つ捦㑡捦〱㤵㈸㠶㘵愵攷㈰㑢ㄴ晢㍢搳㍦挹愸ㅣ㔴㐹晡愷挸㜱㑣㈵改㥦戶摥㐸㝡づ愸摡搳㜳㈰㈵挱慡戳搲敦㘱㉢慡戲搲㜳挰㈵ㅥ㔱㘷晡㡤㡣扡㌷㠸愴㝦㡥摣〰ㄲ戴摢㜸摥㝡㈳改㌹戸㙡㑦捦㐱㤵〴㉢捦㑡捦㠱㤶㈸挲㔹改〷摢㡡晤㥣改㕦㘲㔴づ戶㈴晤换攴挲㈴㑣晦㡡昵㐶搲㜳愰搵㥥㥥〳㉣挹㌲㈸㉢㝤挴㔶っ捣㑡捦㠱㤸㜸散敢㑣晦〶愳搶㠰㐸晡㌷挹㜱摣㈵改摦戲摥㐸㝡づ扡摡搳㜳戰㈵挱昶捡㑡捦〱㤸㈸晡㘷愵攷愰㑣ㄴ㝢㍡搳扦挷愸ㅣ㠴㐹晡昷挹㡤㈴攱搶㝦㘰扤㤱昴ㅣ㠰戵愷攷挰㑢㠲敤㥥㤵㝥慣慤攸㥢㤵㝥㥣慤搸捤㤹晥㘳㐶攵㠰㑣搲㝦㐲㡥攳㌱㐹晦愹昵㐶搲㜳㌰搶㥥㝥ち㌸㐹扦㑢㔶㝡づ捣㐴搱㉢㉢晤㌴㕢戱戳㌳晤攷㡣捡挱㤹愴摦㑣㙥ㄶ〹户㝥㡢昵㐶搲㜳㘰㤶㐹㕦㝡ㄸ戸㠳㘱㔳戸㔴㈵收㈵攷捤摢㕡㕡㔴搶扢攸㤰ㄱ摤慦昸攰慦ㅦ㕤昸捡ㄱ挳㍦晢昱捡㉢㕦昹昸挲㡤㍦㍥ㅣㅦ晥搴戵搷㍥㍥㜱捤挶㡦㝥㤷㕡㕢㜸敦搶㐹㙢㑦㈸㕦㜸挲㌱愹搹〳挷㥤㜰攸搱搳换愷㙤㌷愸㑢㤷慥㕤〷㙣晦㜴慦㝤㐲换㡦戹㕦㍤昶收捥㑤㑡㐶ㅣ㉣挲㜵愳㤱㈳てㄹ㠳㝥㠱㌷㍤扡㤴捥敢散㌲㘴攴攱㈹㈳㙥㤷昱愵㉥㈳搵搹㘵捣㐷〲㘹㠹ぢつ㡥㐴〴㡤㝦改㌲ㅡ㍡扢っㄹ㠹㜸搰㘸戲换昸㐶㤷搱搲搹㘵挸㠸挴㔳㐶摡㉥攳㕢㕤挶搲捥㉥㐳㐶㈶㥥㌲㡥戳换搸慡换㌸愹戳换㤰ㄱ㡡愷㡣攵㜶ㄹ㍦攸㌲㌸慣攸搴て慣㡣㔴㍣㘵㥣㘱㤷昱愳㉥攳散捥㉥攳ㅣ㈴昰㝥㔲捥戵换昸㔹㤷戱戲戳换㤰㤱㡢〷㡤ぢ敤㌲ちっ㌹㝣㜱戸搱愹㑤㤱ㄱ㡣愷㡣换敤㌲ち㜵ㄹ㔷㜶㜶ㄹ㌲㤲昱㤴㜱戵㕤㐶㤱㉥攳摡捥㉥㐳㐶㌴㥥㌲㌸戲㤱愳㘸㐰㤷挱㘱㐸愷㌶㐵㐶㌶㥥㌲㙥戱换㈸搱㘵摣摥搹㘵挸〸挷㔳挶㍡扢㡣愰㉥㘳㝤㘷㤷㈱㈳ㅤ㑦ㄹㅣ昱㐸㔳扡敢㌲ㅥ散散㌲㘴挴攳㈹攳㘱扢㡣㥥扡㡣戶捥㉥㐳㐶㍥㥥㌲㌶搸㘵㠴㜴ㄹ㑦㜶㜶ㄹ㌲〲昲㤴挱㤱㤰㌴攵㜷扡㡣㡤㥤㕤㠶㡣㠴㍣㘵㍣㙦㤷戱㠳㉥攳愵捥㉥㐳㐶㐴㥥㌲㕥戱换搸㐹㤷昱㐶㘷㤷㈱㈳㈳㑦ㄹ㙦搹㘵昴搲㘵㜰㌸搳愹㠷㉦ㄹ㈱㜹捡攰㐸㐹昶㡤摥扡っづ㙢㍡戵っㄹ㈹㜹捡攰㠸㐹捡攸愳换攰昰愶㔳换㤰ㄱ㤳愷っ㡥㥣愴㡣扥㔲㠶攲㜰㐵〶㘵ㅦ㝥慢敦敤㡣㠴㑢〹㥥〴挱〱㠴㈸㍥挸㔲昰㤴㕥ㄴ敦㘷㈹㜸㤲㉤㡡昷戲ㄴ㍣敤ㄵ挵扢㔹ち㥥㠸㡡攲㥤㉣〵㑦つ㐵昱㜶㤶㠲㈷㙢愲㜸㉢㑢挱搳㈷㔱扣㤹愵攰〹㡤㈸摥挸㔲昰ㄴ㐳ㄴ慦㘷㈹昸愵㉦㡡搷戲ㄴ晣ㅡㄶ挵慢㔹ち㝥㌱㡡攲㤵㉣〵扦慡㐴昱㜲㤶㠲㕦ㅥ愲㜸㈹㑢挱挳戹㈸㕥捣㔲昰〰㉢㡡ㄷ戲ㄴ㍣攴㠹攲㙦㔹ちㅥ㠴㐴昱㝣㤶㠲㠷〵㔱㍣㤷愵攰〷㔵ㄴㅢ戳ㄴ晣攸㠸攲搹㉣〵㜷㘶㔱晣㌵㑢挱摤㑢ㄴ捦戸ㄵ摤晥㍦㝢㙦㕡慤 | [5 empty] | 㜸〱捤㝤〷㝣ㄴ㘵晡㝦摥㤰㉣㤹愵㘴㔵㔴㐴挴愰〸㥥㈸㙥㤲摤㙣㠲㈰搲㡢〸㐸戳ぢ㕢㘶㈱㤲〲挹㠲㠰つ㍣㐵㑦戱昷ち搶戳敢搹挵ㄶ搱攳昴挴摥换搹晥戶㥦愲愷愷愷攸㔹晥摦敦昳捥㙣㘶㜶㘶㤷晣晣㕤㍥ㅦ㐳昶㘱㥦晥捣昷㤹㥤㥤㜷收㝤㌳㐵慡愸愸攸㔷晣昰㝦晥㤴昰㑤摦ㄹ换㕡㌳㘶攳㤰搱捤つつ㘶㌲㔳摦摣搴㍡㘴㘴㑢㑢㝣搹攴晡搶㑣ㄷㄸ〴收搴㐳摦㕡㍡愷戵㝥戹㔹㌶㘷㠹搹搲ち愳搲愲愲戲㌲愳ㄸ晡ㅤ慣㔷挸㘶っ㝡ㄹ㈵㈴戰㉡㌲〲㈴㕤㐹捡㐸っ㤲㈰㐹㌷㤲敥㈴㍤㐸㝡㤲㤴㤳㠴㐸戶㈲搹㥡㘴ㅢ㤲㕥㈴摢㤲㙣㐷戲㍤㐹㙦ㄲ收㌷晡㤰散〸搲扤㉦挸捣搱愳愶㈶㡥挲搶捣挸㌴户㤸㝢㔶捣搶㌵て慦慣ㅣ㔲㌹愴慡扡慥㜲㐸㜸捦㡡搱㡢ㅢ㌲㡢㕢捣攱㑤收攲㑣㑢扣㘱捦㡡㘹㡢ㄳつ昵挹晤捤㘵㌳㥢ㄷ㤸㑤挳捤㐴戸㍡ㄱ㡦搴㔶㐶愲搱㜴㕤㕤㙤昷㥤㄰㜹捡攸㔱搳㕡捣㜴敢㝦㉢㘶㍦挶㥣㍡㝡搴㤰㈹㘶收扦ㄵ㜳㘷挴㐴挸㌱捤㡤昱晡愶晦㔲搰㔲昶戴㝡㡣㤹慣㘷昳㑤戳愵扥㘹摥㄰㤴敤〲ㅡ㕣㙣挸㌸㈰㥥㡣户㘶㐶㥢つつ搳捤㌴晢摥扤㤱㤸㤹㉤㘶㔳搲㙣敤搹㌸㜶㘹搲㙣戰搴慤㘵㡤戳攳㉤㔳攲㡤㘶〹摦㤴㌷敡扥㑤㑣㤹㑤㤹晡捣戲ㅥ㡤戳㕡捤改昱愶㜹㈶㑤㑡ㅢ挷㉦慥㑦㤵㤴愸㤲㤲愲㉥㠳晣㡡㤱摥っㄹ搷㤲ㅣ㍤㍦摥㤲ㄱ㡥㕤慢昴戳㜵散㈱㔲戸慢㉣敥㐵ㄵ㌹㕥㙣搳㡣晡挶晤捤㤶㈶戳㠱㐹搸扣挱㌹㐶㠲㠹㠶㍥ぢ㡥扤㌵㙣㡣敡㘶㝤摥戸㈹捣㘲㔴㤰昴〷〹散〲搲㜵昸挸捡愱㤱摡愱挶慥ㄴて〰㔱㈵㙦攱㌳敢㜴攳攷愶㜸㑥扣㜸㑥愲㜸㑥戲㜸㑥慡㜸㡥㔹㍣㈷㕤㍣㘷㕥昱㥣昹挵㜳敡㡢攷ㅣ㔵㍣㘷〱㙣散㥦戲慥㕤㡢慤㥦ㄵ㌷捤㝡㉦㝤㘸昷㔱㈷搶㐶慡㝥ち㡥敡愱昸㌱㤵捦敢㐰扣㌱〶㠱〴㜶〷㤱㌲愲㜵㐳㡤㍦㔰扣〷㠸㔲慦愰っ㤶㌲㘹搲㔷收昲㔳㝦摣晦搲㔳摢扥㥦昲搸㌵㝢㈸㝥捡㈵挶㥥㌴摥ぢ㈴㌰〴㐴㙦㑡攵㔰㘳㙦㡡挳㈰㑡㍤㘷挵愸ㅤ㍣愸攲攵㌳户㥥㝡挵摦づ㍡㜵攳摡㤵㕤ㄵてㄲㄲ愳㡡挶搵㈰㠱〸㠸挴愸慥ㄹ㙡㐴㈹慥〱㔱敡㈹㉢挶昸ㅢ扦㝣敥攲ㄳ㐷㑥㍡敢晤敤ㅥ搹敢㡢挷晢㉢敥㙢ㄲ愳㤶挶㜵㈰㠱愱㈰扡づ挴搸㠷攲㘱㈰㑡㍤㙥挵㌸昲㤳ㄹ㐷昶㝢愳㘹扦㉢挷㉥扤晢挸攱㥢㘶㈹ㅥ愲㈴挶扥㌴ㅥ〱ㄲ搸て㐴搷㠱戶㡣愴㜸ㄴ㠸㔲て摢㜵散㕥摦攷ㅦ捤挳づ㌸㘷昳搴晥㘷扥㌱㝥戹攲ㄱ㑥㘲㡣愱昱㔸㤰挰㌸㄰㠹ㄱ〵ㅥ攳㈹㥥〰愲搴㝤㔶㡣㈱㡦摣晡㔰攵搷㐷㡦戹㝦昶挱㘷㕦㝥搱㐳㡦㉢ㅥ㈰㈵挶㈴ㅡ敦てㄲ㤸っ愲㘳㐴㠶ㅡ〷㔰㍣〵㐴愹扦㔸㌱㙥㍥㜶挸㘷㑤㝢㐷㈷㕥㜳攷㕦㡥晢昲戹㍢摥㔶摣㑦㈴挶㌴ㅡㅦ〸ㄲ㤸づ愲户㈵㌶搴㤸㐱昱㑣㄰愵㙥戶㘲昴攸昵搶㈷捦ㅦ㜱挲搸㤳㍥㝣㈲㜰㘷㉣㔹愶㜸㜸㤶ㄸ戳㘹㝣㄰㐸攰㘰㄰㠹ㄱ㐱㡣㐳㈸㍥ㄴ㐴愹敢慣ㄸぢ㕦㝦晣戸つ㥦扤㍡攱㡣〳扦晤挷攲收㐷㈷㉢ㅥ摤㈵挶攱㌴㍥〲㈴㜰㈴㠸㡥㔱㌵搴㤸㐳昱㕣㄰愵搶㔸㌱晥昳晤扢㍢户㍤ㅡ㥡㝡攳晣扤敢㠷扤戹晤㌷㡡㕦づㄲ㈳㐱攳㈴㐸㈰〵愲㘳〰て㤳攲㌴㠸㔲㤷㔸㌱敥㡢㝥昳攰㠸㐳昶㥦㝡搲㐹扢㕥戵㝣昴搰㘱㡡摦㉤ㄲ㘳㍥㡤敢㐱〲㐷㠱㐸㡣㈸昶て㝥㘶㡣〶㄰愵捥戳㘲ㅣ㄰㑡㘴搶晤戰昵昸搵捦㉣㝢㜷户ㅤ㐶捥㔶晣㙡㤲ㄸ㑤㌴㙥〶〹㉣〴搱㌱戰㝦㉣愲戸〵㐴愹㌳慣ㄸㅦ㥦㌷晣愶㜷㜶㍡㜴昴㥡㜱㝢晥㜹㘱捤敡㝥㡡摦㙣ㄲ㈳㐳攳挵㈰㠱㈵㈰㍡㐶㜸愸㜱㌴挵㑢㐱㤴㍡挵㡡戱攱㡢〵㍢㜷ㄹ昸攵搴搳摥㜹收捡て㥦摥㜱慤攲ㄷ愳挴㔸㑥攳㘳㐰〲挷㠲攸ㄸ挰昴㌸㡡㡦〷㔱㙡愵ㄵ攳昸㙤㝦敤扡敦扣㤹ㄳ㔶摤扢扡捦㤹攷㝦㜲慢攲昷慡挴㔸㐱攳㤵㈰㠱ㄳ㐱㜴っ昴昶㡦ㄴ㥦〴愲搴㌱㔶㡣㝦㙥㍡昰攱昷㠳㐷㡥昹攳㠶捤㝤㕦㌸㝦㐱戳攲搷戲挴㔸㐵攳㔳㐰〲愷㠲攸ㄸ搵㐳㡤㍦㔱㝣ㅡ㠸㔲㡢慤ㄸ㕦㥥昲㐱㜹捦ㅢづㅤ㜷摥㐵愵挹晥㡢捦摤愰昸慤㉥㌱㔶搳昸っ㤰挰㤹㈰ㄲ愳ㅡ挷愰戳㈸㍥ㅢ㐴愹㘶㉢㐶搷㡤愷摦戸㝣㑣㡦〳慥㕡㕢戲昶㤲搷㉥搸㔷昱愴㐰㘲㥣㑢攳昳㐰〲攷㠳㐸㡣㐸㜴愸㜱〱挵ㄷ㠲㈸㔵㙦挵㔸戴㘸晡摡摢て㉢㥥扡慥散昱㠷㙦㌹扤收㥦㡡攷ㄴㄲ攳㘲ㅡ㕦〲ㄲ戸ㄴ㐴挷挰戶㕣㐶昱攵㈰㑡㈵慤ㄸ挹㠳慦㕦户搷慥㠷㡤扢㉢扥昸捣㈳摦扢㜰㠶敡つ戵挴戸㤲挶㙢㐰〲㙢㐱㈴㐶つ㝡㝢ㄵ挵㔷㠳㈸㜵㠴ㄵ㘳㥢㡢晥㍣㘸搰㥦敥ㅢ㜷摡挰昱㜷㝣㝥摤摣敤ㄴ捦㘸㈴挶戵㌴扥づ㈴㜰㍤㠸慥〳㌱晥㑣昱つ㈰㑡ㅤ㘴挵㌸㘶摢㔷㝢慤㜸昲收晤捥㜸㜰㕣㑢搱昳㈳慡㔵ㅦ愸㈵挶㑤㌴扥ㄹ㈴㜰ぢ㠸㡥〱㑣㙦愵昸㌶㄰愵づ戴㘲㕣㌷㜲慢㝦㝤晡昵㈱㤳㉥㈸㝢㜳㔵摤挴㙥户㈸㥥㑦㐹㡣㍢㘸晣ㄷ㤰挰㥤㈰ㄲ㈳ち㑣敦愲昸㙥㄰愵昶户㘲ㅣ㔶搲㜵挵扥㠳㤶㡦㕥㜷㕢收挱ㄱ㕢㝤扤慡晢扤㔰ㅦ㘸㝤攵㡤㘹㠹ㅦ㡤昳㠶昶㔳㤲慡㈱㘱晥摢昲戹ㄸ㑥挵搲搱㜴㉣㕤㔹㤹㡡㠶攳搵昱搲ち㠴敤攸ㄹ〰㜷搱敥改㠳敡㥢㔲捤㐷换㈹㐱昷昴戸晡㠶㡣搹㈲㑣㜹ㅡ晦改搳ㅡ攱㝢愴挷㉥挵昹㘰㔲㥦㍤昴㑡㡦㌶㕢㌲㌸㡦捡㉣㙢㍦愵攸㍢㉡摥㙡戶戳㠳慤搸愳㥡ㄷ㌷愵㕡㜷昴㔷捥挸挴㌳㘶㥦㕣㕤㝢㄰㡦摢っ㥣㘳㤹慤㔲㔲扦㕣户搹昱㠶挵收挸愵昵㕡扤㔳㡥ㅡ㘷㕢捤㠹晣摡㜱㉤收愲慣搶㔳搱㐸っ〱㤶㐸㙣捦㔶㙡㤵慥慢㘲昴晣收㔶戳㐹捡ㅢ摣㌸慤㍥戹挰㙣㤹㘱㜲〰㘱愶㘴㔳户愵捡㍡攵ㅢ㍣戵〹ㅢ㡡㤳戸搴㉥㑥㈹㠱㌶㥢㔲㘶ち昵㉥〴捡换㘶挶ㄳつ收㜶㉥ㄳ㥤ㄳ㡡ㅤ㕣攲㜱捤挹挵慤愳㥢㥢㌲㉤捤つ㙥捤挸搴㤲㌸㑥㌳㔳〷㌴愷捣ㄲ昹㈹搲㔴ㄵ㜵改愲㔴搱敥㝥攷㙢㡣摤捡㌳㍡挷㑥挲昳挶挲挶㡥㥤㠸挶扥㘷㠲搹挸㜸攳搸挹㘸晦㠷㠲㤵㌸㜷㐲㕡㠷ぢ㕡晢散愴㜴敡敤晥攰つ㤹㡥晥愰てつ㈶㍦㤵挵〳昲㠷㙣摦㉦户㔰愹愳㉢ㅣ㉦搲扡〰㘸ㄲ㌶扢敦㜵慥㜱㜱昱㌶搶搶㡦㕤㠲挱挴㠴㜸㔳慡挱㙣㈹㌸摡㔵慣挸戸㡦攴㝥㤲〷㐸搶㤱㍣〸㔲㍡〶挷戸扣㠸㤶挰㐲㉤㔵换㑡㡦慥㑦㘵收〷收㥢昵昳收㘷㈰挳㈸戹慣㡣㜰㝢㝥㡣㠷㈱㌲ㅥ㈱㜹ㄴ㈴ㄸ㉣ち戴攱晦愲㐰搰㜸っ晦㠱㉦敤㡦晦晦昷㘳㤷㘲㜸ㄹ㌲㔴挲㔸戶戵戴ㄱ㈳戲搶㉥㕤晣戶㝣㐲扣㜵㝥㠶ㅦ扡挲㑡挶㕢㑦昲㌸㐸昷㈷㐰愶㑣㌰ㅢ昰㤱晤㙦つ㠳㑢㜷㐵捣㉤づ户㜸捡戳㕤攳㡣㘵㑤挹昹㉤捤㑤戸ㄸ㌱㈶㥥㠹㡦㑣㘲㑣搹慡攲㠱挶挹捤愳ㄷ㘷〲㡤ㄳ敡昱㕦昷挶改收㐲㌳㥥ㄹ㡤㐳㜲愶㐷攳㘴㡣㐷攵㤸㌹㌱戵戴戴㔱て㈵挷㤸慤㐹㠳㘳捥㠹㌸〴㉤つ攰ㅤ㡥愹摤ㅢ㜹㔰㌱㤷㘶ㄸ扡㙢攳戴㌸挶慣ㄹ〳㐶㠳挵㑢扦愳㘷て㤱搹摥㐱㡢㐳㠴㤰扣㜵㐴改㈶〲ㅤ愹㠸㝢〹扥㉤昱戵㕡㘲搱摣㑦换慣㑣㝤㐳敢㄰ぢ摥㈱㘳㥡㜱㑤挲㤴换㌱㠴㍤㄰挰捥ㄴ㈸搸慣摣て㌵〷慤㔳㤳〹ㅤㄶ愵㡣㙦㘹㕥扣戰ㅦ㘲晤户攲㌰㔶㤱昱㔷㤰㌵㕦摦戴捦㙥㔷摣晥慢昵晦〹昸戸挸㡦戱ぢ㉤摡㐰挸攲㍦昹㌱㥥挴㝦挱㐲扡搲〱戰昰㍤慡收ㄹ㕦㤷挲扥㝢㈳戶㜶㘶㡢㈹ㄷっ捡㠴㔹戶搰散搱㜸㔰㜳换㠲㐴㜳昳〲㌶扦愷㜰慤昳㑤㌳挳㔱㜸㌷敢愲〳摦㉢愵扡㜴㜱㡤戵ㅤ挳昵㥤ㄱ㍦戰ㄱ愴挷挸㠶㠶ち㍢㘲㙢攰ㄹ㠸扡攰摢㈳昰㉣摥㠴㙡挲搵㤱搸㑣㥥摡㔴て㔹摡搰摡愸㉡戱搵ㅣ㌷㍦㝣捤挷㕦㕤㝥搸㥡㈹㜷晣㝣摤昳㤳敦㍥晤ㅣㄵ戶ㄴ㥥㐱昹㐰挴愹挰换㜸㠱攴㐵㤲㤷㐸㕥㈶㜹〵㐴敤〱㔷ㅥ㡦昰摥晤㘳扣〶摥㜸㥤攴つ㄰ㅣ㐵〴㜹ㅣ㔴摥搲慣ㅡ㠴晦㜹㘰㌱摥㈶昹〷㠸攲㈰㥦ㅦ挱㈲攳ㅤ㤰扣㝤摣㥤ㄶ㙤㈰㐸㥣捤㙣扣て㐱搰㈸愰㔳㝢挰㠲扤㌴㠸㥤㐱戴っ㈲愵㝡㈳㡣㉦㌰摢㕢ち捦㤵㠶㍤攱㔶㐱晦捦㐸㍥㈷搹㐴昲〵挹㤷㈰㙡㉢戸晡〳昳ㄵ㙤扥㈶昹ㄷ㠸〳㤸㙦㌵慢昶挲晦〲捣扦㘹昴ㅤ㠸摡ㅢ㐴〳昳㍤摥攵〵㘶〸ㅤ摡㐰㤰扣ㅤ㤸ㅦ㈱〸ㅡ〵㜴㉡っぢ㍦㘰㝥晤㈵て㌰扦㔸ち捦攵㤳㉡㐴慡挰换攸愲㐰㜸㘱搷㈸㈵〹㤰㜴〵㔱㥢攱敡て㡣㐱㥢㈰㐹㌷㄰〷㌰㍤㌴慢慡ㄱ戸㍦㠳昷愴㔱㌹㠸㡡㠲搵挰㠴挰收〵㈶㐲慦㌶㄰ㄷ㌰摢挰㈵㘸ㄴ搰愹ㅡ戸昸〱昳㜱㍥㘰㍥戲ㄴ㥥㙢㐲戵㠸㔴㠱㤷搱ㄷ㐹㡤㥤㐸晡㤱散㑣㔲〱愲摥捤ぢ捣㉥戴搹㤵㘴〰㠸〳㤸㠱㥡㔵㜵〸摣㥦挱〷搱㘸㜷㄰戵て㔸つ捣ㅦ挰收〵㘶㈸扤摡㐰㕣挰散〹㤷愰㔱㐰愷㠶挱挵て㤸㘷昲〱戳搱㔲㜸㉥㜴敤㡢㐸ㄵ㜸ㄹ㔱㈴㌵㙡㐸㘲㈴戵㈴㜵㈰㙡㐳㕥㘰昶愱捤㌰㤲攱㈰づ㘰㐶㘸㔶㡤㐰攰晥っ扥ㅦ㡤㐶㠲愸㤱㘰㌵㌰愳挰收〵㘶㍦㝡戵㠱戸㠰ㄹぢ㤷愰㔱㐰愷㐶挱挵て㤸扢昳〱㜳㤷愵ㄸ㥦㝢昵㙥っ㈲㔵攰㘵㑣㐱㔲㘳㉡挹㌴㤲〳㐹愶㠳愸㕢昳〲㌳㤳㌶戳㐸㘶㠳㌸㠰㌹㔸戳㙡㉣〲昷㘷昰㐳㘸㜴㈸㠸攲搵㐰つ捣㘱㘰昳〲㌳㡥㕥㙤㈰㉥㘰㡥㠴㑢搰㈸愰㔳ㄳ攰攲〷捣㘵昹㠰戹搴㔲㜸㉥㐹㑥㐲愴ち扣㡣㜹㐸㙡捣㈷愹㈷㌹㡡㘴〱㠸㍡㍦㉦㌰㡤戴㘹㈲㘹〶㜱〰戳㐸戳㙡㝦〴敥捦攰㉤㌴㙡〵㔱〷㠰搵挰㘴挰收〵㘶㌲扤摡㐰㕣挰ㅣつ㤷愰㔱㐰愷愶挰挵て㤸ㄳ昳〱戳搲㔲㜸慥戳㑥㐳愴ち扣㡣ㄵ㐸㙡慣㈴㌹㤱攴㡦㈴㈷㠱愸㘳昲〲戳㡡㌶愷㤰㥣ち攲〰收㌴捤慡〳ㄱ戸㍦㠳㥦㑥愳搵㈰㙡〶㔸つ捣ㄹ㘰昳〲㌳㥤㕥㙤㈰㉥㘰捥㠶㑢搰㈸愰㔳㌳攱攲〷㑣㝤㍥㘰收㕢ち捦挵攳搹㠸㔴㠱㤷㜱〹㤲ㅡ㤷㤲㕣㐶㜲㌹挹ㄵ㈰㉡㤱ㄷ㤸㌵戴㔹㑢㜲ㄵ㠸〳㤸㙢㌴慢づ㐲攰晥っ㝥㉤㡤慥〳㔱㠷㠰搵挰㕣て㌶㉦㌰〷搳慢つ挴〵捣㡤㜰〹ㅡ〵㜴敡㔰戸昸〱㌳㉤ㅦ㌰㔳㉤㠵攷㡡昸攱㠸㔴㠱㤷㜱㈷㤲ㅡ㜷㤱摣㑤㜲て挹扤㈰㙡㘲㕥㘰敥愷捤〳㈴敢㐰ㅣ挰㍣愴㔹㜵〴〲昷㘷昰㠷㘹昴〸㠸㥡〳㔶〳昳㈸搸扣挰ㅣ㐹慦㌶㄰ㄷ㌰敢攱ㄲ㌴ち攸搴㕣戸昸〱ㄳ换〷㑣㡤愵昰㕣收㑦㈰㔲〵㕥挶搳㐸㙡㙣㈴㜹㠶攴㔹㤲攷㐰㔴㌸㉦㌰㉦搰收㐵㤲㤷㐰ㅣ挰扣愲㔹㤵㐴攰晥っ晥㉡㡤㕥〳㔱㈶㔸つ捣敢㘰昳〲㤳愲㔷ㅢ㠸ぢ㤸户攰ㄲ㌴ち攸㔴ㅡ㉥㝥挰昴换〷捣㑥㤶挲㜳敦㘲㍥㈲㔵攰㘵㝣㠸愴挶㐷㈴ㅦ㤳㝣㐲昲㈹㠸摡㍥㉦㌰㥦搱收㜳㤲㑤㈰づ㘰扥搴慣攲慤㤰晥っ晥㑦ㅡ㝤〵愲ㄶ㠰搵挰㝣つ㌶㉦㌰㐷搱慢つ挴〵捣户㜰〹ㅡ〵㜴慡〱㉥㝥挰㤴收〳愶挴㔲㜸㙥挸㌴㈱㔲〵㕥挶捦㐸㙡晣㐲昲㉢㐹㔱㌱㠸〲㔱扦晣㥣敦捣户ぢ㙤㑡㐸㑡㐱ㅣ挰㜴搵慣㙡㐶攰晥っ㕥㐶㈳㑥㜷㔰㡢挰㙡㘰㠲㘰昳〲戳㤰㕥㙤㈰㉥㘰㝡㌰慥㔱㐰愷㕡攰攲〷捣㈶㙣㠴敦㔸改㜳㑢攱戹换㤴㐱愴ち扣㡣敤㔸晢昶㈴扤㐹㜶㈰改〳愲㍥捡ぢ㑣㕦摡散㐴搲て挴〱㑣㠵㘶搵㘲〴ㄶ㘰晡搳㘸ㄷ㄰㜵㌴㐴ㅡ㤸㕤挱收〵㘶〹㑢㙡〳㜱〱㌳㤰㜱㡤〲㍡戵ㄴ㉥㝥挰扣㤴て㤸ㄷ㉤㠵攷搶搹㜲㐴慡挰换搸㥢戵㠷㐹㉡㐹慡㐸慡㐱搴挶扣挰㐴㘹㔳㐳ㄲ〳㜱〰㔳愷㔹㜵っ〲ぢ㌰㐳㘹戴て㠸㍡づ㈲つ捣㌰戰㜹㠱㌹㤶㈵戵㠱戸㠰ㄹ挱戸㐶〱㥤㍡ㅥ㉥㝥挰慣换〷捣〳㤶挲㜳㍦㜰〵㈲㔵攰㘵㑣㘰敤ㄳ㐹㈶㤱散㑦㌲ㄹ㐴摤㤵ㄷ㤸㈹戴㤹㑡㌲つ挴〱捣㜴捤慡㤵〸㉣挰捣愰搱㑣㄰昵㐷㠸㌴㌰戳挰收〵收㐴㤶搴〶攲〲收㘰戸〴㡤〲㍡㜵ㄲ㕣晣㠰戹㉡ㅦ㌰㙢㉤㠵攷㈶攷㉡㐴慡挰换㠸㈳愹㤱㈰㐹㤲愴㐸㑣㄰㜵㘹㕥㘰收搱㘶㍥㐹㍤㠸〳㤸〵㥡㔵扣㘷㉡挰㌴搰愸ㄱ㐴昱愶愹〶愶〹㙣㕥㘰㑥㘵㐹㙤㈰㉥㘰ㄶ㌱慥㔱㐰愷㑥㠳㡢ㅦ㌰愷收〳收ㄴ㑢攱戹㜳扢ㅡ㤱㉡昰㌲㤶戳昶㘳㐸㡥㈵㌹㡥攴㜸㄰戵㌲㉦㌰㉢㘸戳㤲攴㐴㄰〷㌰㈷㘹㔶㥤㠱挰〲捣挹㌴㕡〵愲捥㠲㐸〳㜳ち搸扣挰㥣挹㤲摡㐰㕣挰㥣挶戸㐶〱㥤㍡ㅢ㉥㝥挰㌴攷〳愶挹㔲㜸㙥㐷㥦㡢㐸ㄵ㜸ㄹ攷戱昶昳㐹㉥㈰戹㤰攴㈲㄰㌵㍦㉦㌰㤷搰收㔲㤲换㐰ㅣ挰㕣愱㔹㜵ㅥ〲ぢ㌰㔷搲㘸つ㠸扡〰㈲つ捣㕡戰㜹㠱㌹㥦㈵戵㠱戸㠰戹㠶㜱㡤〲㍡㜵㈱㕣晣㠰㤹㥤て㤸㔹㤶挲㜳㡦晤㘲㐴慡挰换戸㠵戵摦㑡㜲ㅢ挹敤㈴㜷㠰愸愹㜹㠱戹㤳㌶㜷㤱摣つ攲〰收㕥捤慡㑢㄰㔸㠰戹㡦㐶昷㠳愸换㈰搲挰㍣〰㌶㉦㌰㤷戲愴㌶㄰ㄷ㌰て㌱慥㔱㐰愷㉥㠷㡢ㅦ㌰挳昳〱㌳捣㔲㜸㈶づ㕣㠹㐸ㄵ㜸ㄹ㝦㘵敤ㅢ㐸晥㐶昲㈴挹㔳㈰慡㈶㉦㌰㑦搳㘶㈳挹㌳㈰づ㘰㥥搳慣㕡㠳挰〲捣昳㌴㝡〱㐴㕤〵㤱〶收㐵戰㜹㠱㔹换㤲摡㐰㕣挰扣挲戸㐶〱㥤扡ㅡ㉥㝥挰っ挸〷捣慥㤶挲㌳ㅢ攲㕡㐴慡挰换㜸〷㐹㡤㜷㐹摥㈳㜹㥦攴〳㄰戵㔳㕥㘰㍥愴捤㐷㈴ㅦ㠳㌸㠰昹㔴戳敡㍡〴ㄶ㘰晥㠷㐶㥦㠱㈸捥慥搰挰㝣づ㌶㉦㌰搷戳愴㌶㄰ㄷ㌰㕦㌲慥㔱㐰愷㙥㠰㡢ㅦ㌰摤昲〱ㄳ戴ㄴ㥥㈹ㅥ㌷㈱㔲〵㕥挶昷慣㝤㌳挹て㈴㍦㤲晣〷㐴㤵攴〵收㘷摡晣㐲昲㉢㠸〳ㄸ搵㐵㔸㜵㌳〲ぢ㌰挵㄰ㄸ㕤㐰搴慤㄰㘹㘰㑡挰收〵收ㄶ㤶搴〶攲〲愶㉢㕣㠲㐶〱㥤扡つ㉥㝥挰晣敢愷㍣㘷扥㕦㕢ち捦扣㤵㍢㄰愹〲㉦㈳㠴愴挶㔶㈴㕢㤳㙣㐳搲ぢ㐴㝤づ㔷晦㡢攱摢搱㘶㝢㤲摥㈰づ㘰晡㘸㔶晤〵㠱〵㤸ㅤ㘹搴ㄷ㐴摤〵搱慥㜸攱㤴ㄹ㙣㕥㘰敥愴㐵ㅢ㠸ぢ㤸ち戸〴㡤〲㍡㜵㌷㕣晣㠰㜹㈳ㅦ㌰慦㕢㡡摣挹㌸愵昷㈱㔲敥つ㐷㤹戰㥡㥤愶攰㤸〰搱ㄳ挶㠱昴慣愶晡㑣㙢户昴挸挵㤹收㜱昵㤹㌱慤㤹敥㘹㄰扣ㄵ㤷㍥㜲㐷摦攱㌴㌸㍤扢摥㍣㝡㈶㙥戹敤散㔵㘱㉥敦攸挵慤㤹㘶戹㤷摡捦慢ㅦ搳㍣愵㌹㌳愶扥㜵㘱㐳㝣搹〰ㅦ戵搶ㅣ㌴摦㙣挲ㄴ㤳ㄶ捣㌴搹㤲㔱昳挲㠵㘶捡愷挶ㄹ捤㡢㕢㤲收挴㌱扦㠷㐹㉡㑡摦ㄴ㉥挲㝤㐷愵㡡搴㙥昹㈷㘵㌸㜰摦〹扤㈹挶扤㑡昵ㅢ攷㌸戴挱ㅦ搳㝡戱敢ㄵ㈱㈷㜶㜳晣ㄴ㤵摥て戶昰敥攱㤸昲搲つ挶挱㌴㕡慡㘵㍤慣㌹㔵ㄳ㥢㕡敢㔳㘶搰攲づ愸㙦敡㘹扤㥤扡㌸攳搲挴㤷㙥㘳㘹㜰㌳㜵㙡ㄳ摡㥥㡣户愴㝥てㅤ挱㠶攱㐷户㐳〵昰敦户㠱慣挳ㄴㄵ㝤挵换ㄱ晣昹敡〴〱扡愸昴〱㌰扥昷戵戳ㅦ㐳扣㜱捣ㄶ㉡㠷㝤て㐲㥤ㄵ㤷㤱㍢挰㡣㌷㐹〷㘶㘴㔲㘳捣㈵㍤挵挲挴㡥㡤愹昳つ收㌶㙥㔶愶㌷ㄸ改㤱㠹搶收㠶挵ㄹ戳㘷昶㥤㝣挰㡤昴㜴戳㈱捥㤹㕦摤戳敦愶㈵㌳㤸ㅢ㤷㡤挷㔹㕤扦㥦敥〰㤱ㄲ慢㐳㑡㝡ㄴ㈸戰攳扡㌷㠲㥦㥤摦搸㔱㌴㌲㉤㍦㕦㡥㔰㤷㕥挲㥦ㅢ㐷ㄴ搹㙦慣て搱㍡㠴敦昸搴㉥㝥㡡戶戱㘷ㅣ敡㈳㥢ㅣ戴扡摢㌲捥慡敡㤱㤶攳ㅤ愶㑥㜲搵㐴㌹㍦㌶つ㔸搲㤲愹㑦挶ㅢㅡ㤶昵㑣㑦㙣㑡㌶㉣㑥㤹㤳攳〹戳挱㍥㔶㌷户㌴晥㑥晡㔵挲摤㕦昷慡〰㉥搶㝣户㠹㔸㙡㘴㑦㈴晢捤㠷户㈲㘳㌰㡥㙣昲㔵㡢ㄸ晡搸昶㈰㡡昸㕦捦愱ぢ挲㘹敢昶ㄹ愰戲㄰〵㠷㌴㡦㠸挷㌲捥㌱捡㑥挳㤳㑦㥢挳㙣㜲昳攴㘶㑣㤱㑣㌹㐴ㄳ敡戵攸㜷昳㤹㤲ㄶ〵〲㠱摦晡愵〲慣昰昳㤵㌵晦〱〷㍢捤㡦攰㔹ㄴ扦㕤ㅥ〶㥦㍢㍢挹㜱昲㈱摦昷㜲〰っ挱戰㥣㐷㉦㝤戲㌰戳㍥搳㘰㜶㑢㡢㕥摥㤷昱攳㐰㌴扢愶㘷捥挷㑣㥦㌱㍤搲攳㕢敡㔳つ昵㑤㈶㑦㍣㌰㘵㤷㡢㝦㈶㥢昳㌰戹㜴㕡㜳㙢㍤搷戴昵㐸捦㙣㠹㌷戵㉥攴㠴慥攴戲慤㕤㥣㌴慢㌴㍤慡扥〹ㅦㅥ㥤㤳敦换搳㌳收㌷ㅦ㡤㘵㜱㡢ㅢ㥢挶挷ㄷ戶晥㉥ㅡ㘵㝤㤵〰㈱晤㠹㉡㔶挵挵慡慣戸散户㝥㐷㘱て㐷挸㉡挴㉢㈶戱㕡昵〸摥ㄵ昸慣戲㑢搶搴㕥㝥㔶㔹㤳㙢㠹㤷敦㕣挳散㥡㐲ㅥ㝦㡤扤昰〱敤㍥〴㘴搲昸㔹ㄳ摢㈷㠴晦㥦ㄶ攸㤵㍥㡡挸〵扥〶㘴户挸捥㍥摤ㄶ挶㍤昵慥㐲ㄹ昷ㅣ㐳㍡㑥㉥㜷昷ぢ愶挵㠶㝢㈲扥㌹㘹捥户攳㌰㔷戰㍢㍥昸㌸散㘲㡥㈵㡥户㍤㌵挳㔳戸挶㜸㐳慢愵ㅢ摤摣搸ㄸ攷慥挵摤㜲〶㡥搹㘶㤹㥣㑦攳㐸㘲愴㐱㘴晦戳㐴昱愵㄰挵㤷㡡〸㕦挵㥣㔱㉥敦ㄹ慢㜹㕥扣愵㍥㌳扦戱㍥㔹㐶㠶戳扥㝦ㄷ晢㈴㜶愱ㄲ㠰㘹晦挸㡥㠹㤳搳摣昹㥣㝡ち㈲摡㍤〴攳〵㐲挷昶㘳捦㉤㤶敦㙦昵ㅢ愷敢ㄶ㈹㈵〷㝡㈳㡣㘸愵ㄸ换㐲㘰㝤㐸ㅣ㈷㕥㤰挸㐱㐸㍤㐶〳扣㡣㑡㤸摢㍦㈵敢昱慥攰慣捡慥㌰〸㑥㙥㡥愷挶㘱㘱㐰㜳㑢㔷㙢㐱㘹ㄹ㕡换㐳㑡㑢㠸㌳㘹㐷㘳捡㌹愶戲㉦挱昹㙦㑢ㄹ〵㌳㌰㐷戵㠴㜳㜰〳扡㠷晣搰ㄶ㤵㤶㜶㉢昳换㌵搱㡥㌵挰㥡㜱攸㕣㤰㍢搱ㄳ㝦搳㠱戵㈳戸㈱挱㈰㑦㈱㡣㉡㙣㡥㔱つ愲ㅥ〷换敤挹㌱㠸搰㈰ち㔲晡㔷㈸㜳㍦㈵㜹㘷㥤挲愱愸戴㤱戳㘱换ㅡ戹㌹㌸搵〸㘰㡥㉣㘶搵〲㤲㐰户戲㈷愰㌷㙡㘰昵捣挶㡤挳昱扥㐸㍤〹㘲攷攷㙥㘱ㄵㄸ㘳晥㕡㄰昵〲㠴ㅣ㠸㑡摢㡡㡣愱㑣搱㍥〸㔱㉦㠲攵㐰挴晥㜱㜴搱敡攱㑢㔰昱ㄴ㥡㡤摣搲改㤸㝡ㄹ㜶㍣㈵挳扤ㄸ㔶搰㠶㜷昶㌹㠱㝡〵っ捦ぢ昴㑦摥㙦㉥昵ㅡっ昸敤㔵攴㝢戴㔴慦㐳挳㈳愶㌱㥣㥢昷〶摥昱㐰㤴摤㌱㐷㐰扡攵ㅤ昳㉤㝡攰攵摡㌱搵摢㤰搸㘰㍡扡㍤㤲㥢㌲㡡搹晥攱㙦㌰㥡〶㘳㘸昰づっ搸㜱㘳㉣戸㙣㤳摥㜷戸㌹㥡㌴㡥㙥攳改昶ㄹっㅣ㑤㥡〸㤹戳㐹㥦㠳㉤摣愴㑤戰攸㜰㤳扥㠰戱㙥搲㈴㔶搰〶㌶摢愴㉦挱㜴愴㐹㕦挱慥㐰㤳扥㠶㕡㥡㌴㤹㥢昷㉦㜰慥㈶㑤㠱㜴换㑤晡ㄶ㙥摥㈶晤ㅢ㔲㥦㈶㑤攳愶ㅣ挸㙣摦昹ㅢ㑣愷挱っㅡ㝣て〳㘹搲㑣㜰搹㈶晤攸㜰㜳㌴㘹ㄶ摤㘶搳慤ぢ㙡㜱㌴改㘰挸㥣㑤攲㠹㜷攱㈶㤵挲愲挳㑤ち挰㔸㌷改㄰㔶搰挶㘴搶搹戵敡ち㕤㐷㥡挴愹愶〵㥡挴㐹愸搲愴挳戸㜹摤挰戹㥡㜴〴愴㕢㙥ㄲ㘷慤攲㌷攷㤳搴ㄳ㈲㥦㈶捤攱愶捣㘵戶㜲㝦㠳㌸つㄲ㌴攰㐴㔷㘹㔲ㄲ㕣戶㐹㥣换㙡挷㜵㌴㈹㐵㌷㤳㙥㥣㜷敡㘸搲㍣挸㥣㑤摡〹敡挲㑤攲㜴搵づ㌷㘹㘷ㄸ敢㈶捤㘷〵慥㈶㔵㐰搷㤱㈶㜱摡㙢㠱㈶敤ち戵㌴改㈸㙥摥〰㜰慥㈶㌵㐰扡攵㈶つ㠴ㅢ㝥㜳㥡㌴〸㈲ㅢ㑣㙡慤敦㡥㈶㙥㑡㌳戳㜱㡡慤㡦挱㐲ㅡ㉣愲〱㈷摤㑡㤳㕡挰㘵㥢挴㜹戵戶㥢愳㐹慤㜴攳摦戸㔰㥣〳敢㘸搲ㄲ挸㥣㑤攲散搸挲㑤攲搴搹づ㌷㠹㔳㙣㜵㤳㡥㘶〵慥㈶㜱收㙤㐷㥡挴㈹戸〵㥡挴挹戹搲愴㘵摣扣攱攰㕣㑤㍡〶搲㉤㌷㠹㈷ㄸ昸捤㘹搲㝥㄰搹㘰㔲㙢㌵改㌸㙥捡昱捣㌶搲摦攰〴ㅡ慣愰〱㈷〰㑢㤳㔶㠲换㌶㘹慣挳捤搱愴ㄳ改昶㐷扡㑤㠱㠱愳㐹㈷㐳收㙣搲㔴愸ぢ㌷㠹搳㜸㍢摣㈴㑥昷搵㑤㕡挵ち㕣㑤攲㉣攰㡥㌴㘹㈶散ち㌴㠹ㄳ㠵愵㐹愷㜲昳㌸㘳搸搵愴搳㈰摤㜲㤳㌸戳ㄸ扦㌹㑤攲昴㘲㥦㈶慤收愶㥣挱㙣㥣㝡散㘳㜰㈶つ捥愲〱㈷㈳㑢㤳捥〶㤷㙤ㄲ攷ㅢ摢㙥㡥㈶㥤㐳户㜳改㌶て〶㡥㈶㥤て㤹戳㐹㥣㌵㕣戸㐹㥣㔲摣攱㈶㜱敡戱㙥搲〵慣挰搵愴〵搰㜵愴㐹㥣㥡㕣愰㐹㑤㔰㑢㤳㉥攲收㌵㠳㜳㌵改ㄲ㐸户摣㈴捥㜲挶㙦㑥㤳㌸搵搹〶㤳㕡敢㤳㜴ㄹ㌷攵㜲㘶攳㌴㘸ㅦ㠳㉢㘸㜰㈵つ㌸昶㤶㈶慤〱㤷㙤ㄲ攷㍥摢㙥㡥㈶慤愵摢㔵㜴㕢〱〳㐷㤳慥㠱捣搹愴㤵㔰ㄷ㙥ㄲ愷㌷㜷戸㐹㥣〶慤㥢㜴㉤㉢㜰㌵改㈴攸㍡搲愴㔵戰㉢搰愴㔳愰㤶㈶㕤捦捤攳㑣㙡㔷㤳㙥㠰㜴换㑤攲㡣㙢晣收㌴改㜴㠸㙣㌰愹戵㥡㜴ㄳ㌷攵㘶㘶攳㤴㙣ㅦ㠳㕢㘸㜰㉢つ㌸㐹㕢㥡㜴ㅢ戸㙣㤳㌸て摢㜶㜳㌴改㜶扡摤㐱㌷捥㤹㜶㌴改㑥挸㥣㑤攲㙣敡挲㑤攲㔴敢づ㌷㠹㔳戲㜵㤳敥㘲〵慥㈶㕤〱㕤㐷㥡戴〶㜶〵㥡戴ㄶ㙡㘹搲㍤摣扣慢挰戹㥡㜴ㅦ愴㕢㙥ㄲ㘷㝦攳㌷愷㐹搷㐲㘴㠳㐹慤搵愴〷戸㈹敢㤸敤㍡㝦㠳〷㘹昰㄰つ慥㠷㠱㌴改㘱㜰搹㈶㜱㑥戸ㅤ搷搱愴㐷攸昶㈸摤㌸㝦摢搱愴挷㈰㜳㌶㠹㌳扢ぢ㌷改㙥㔸㜴戸㐹㥣ㅥ慥㥢戴㥥ㄵ戸㥡挴㔹攳ㅤ㘹ㄲ愷㡦ㄷ㘸ㄲ㈷㤶㑢㤳㥥攰收㜱㠶戹慢㐹ㅢ㈰摤㜲㤳㌸ㄳㅤ扦㌹㑤㝡ㄸ㈲ㅢ㑣㙡慤㈶㍤挹㑤㜹㡡搹㌸㔵摤挷攰敦㌴㜸㥡〶㡦挲㐰㥡戴ㄱ㕣戶㐹㥣㥦㙥扢㌹㥡昴っ摤㥥愵摢搳㌰㜰㌴改㜹挸㥣㑤攲㉣昳挲㑤攲ㄴ昴づ㌷改㔹ㄸ敢㈶扤挰ち㕣㑤㝡づ扡㡥㌴㠹㔳搹ぢ㌴㠹㤳摣愵㐹㉦㜱昳㌸摢摤搵愴㔷㈰摤㜲㤳㌸㉢ㅥ扦㌹㑤攲搴㜸ㅢ㑣㙡慤㈶扤挶㑤㜹㥤搹㌸㙤摥挷攰つㅡ扣㐹〳㑥愴㤷㈶扤〵㉥摢㈴捥㤵户摤ㅣ㑤㝡㥢㙥晦愰摢㠷㌰㜰㌴改㕤挸㥣㑤晡〸敡挲㑤晡ㄸㄶㅤ㙥搲㈷㌰搶㑤㝡㡦ㄵ戸㥡挴搹昴ㅤ㘹ㄲ愷搵ㄷ㘸搲攷㔰㑢㤳㍥攰收㜱收扤慢㐹ㅦ㐲扡攵㈶㝤〹㌷晣收㌴改㥦㄰搹㘰㔲㙢㌵改㘳㙥捡㈷捣挶㈹晣㍥〶㥦搲攰㝦㘸挰㐹晤搲愴捦挰㘵㥢昴慤挳捤搱愴捦改戶㠹㙥㍦挳挰搱愴㉦㈱㜳㌶㠹戳敦ぢ㌷改㔷㔸㜴戸㐹㐵挵㜶㤳晥挹ち㕣㑤㔲搰㜵愴㐹㥣攲㕦愰㐹㈵㔰㑢㤳扥收收戱ㅦ慥㈶㝤〳改㤶㥢挴搵〲搸慥㥣㈶㤵㐱扡ㅥ搲㥣ぢ戱晦收愶㝣挷㙣㠶扦挱昷㌴搸㑣〳㉥㌰㤰㈶晤〰㉥摢愴ㅥづ㌷㐷㤳㝥愴摢㝦攸挶昹晥㡥㈶晤っ㤹戳㐹摢㐳㕤戸㐹㕣㈶搰攱㈶敤〰㘳晤㐹晡㠵ㄵ戸㥡搴〷扡㡥㌴㠹换つち㌴㠹ぢㄱ愴㐹㥣㉡愳晡㠱㜳㌵愹ㄸ搲㉤㌷愹〲㙥摥㈶昵㠷㜴扤户㐹昸〳㠳㔸ㄳ挲㙣扢昸ㅢ〴㘸搰㤵〶㕣散㈰㑤㉡〳㤷㙤搲㐰㠷ㅢ攴昶㈷㤴㝦ㄵ搳〸搲㡤㙢てㅣ㑤敡㑥㈳挷㔵㜰慥㑡㈸摣㈴㉥㔹攸㜰㤳戸戴㐱㌷愹〷㉢㜰㌵㠹㉢ㅥ㍡搲㈴㉥㝤㈸搰㈴㉥㡡㤰㈶㤵㜳昳㘲攰㕣㑤摡ち搲㉤㌷愹づ㙥摥㈶つ㠵㜴扤户㐹摢㜰㔳㝡㌱ㅢ㤷㔹昸ㄸ㙣㑢㠳敤㘸挰㠵ㄷ搲愴敤挱㘵㥢挴戵ㄵ戶ㅢ攴㜶㤳㝡搳㙤〷扡㑤㠰㠱愳㐹㍢搲挸搱愴㠹㔰ㄷ㙥ㄲ㤷㑦㜴戸㐹㕣㘶愱㥢搴㤷ㄵ戸㥡挴搵ㄷㅤ㘹ㄲ㤷㘱ㄴ㘸ㄲㄷ㘸㐸㤳晡㜱昳戸㔲挳搵愴ち㐸户摣㈴慥攸昰㌶㠹换㍡搶㝢㥢戴ぢ㌷㘵㔷㘶攳㤲てㅦ㠳〱㌴搸㡤〶㕣〴㈲㑤ㅡ〸㉥摢㈴慥昳戰摤㈰户㥢㌴㠸㙥扢搳㉤づ〳㐷㤳昶愰㤱愳㐹〹愸ぢ㌷㠹㑢㌹㍡摣愴ㄴ㡣㜵㤳〶戳〲㔷㤳㑣攸㍡搲㈴㉥〹㈹搰愴昹㔰㑢㤳昶攲收搵㠳㜳㌵㘹㙦㐸户摣㈴慥㉥昱㌶㠹㑢㑣搶㝢㥢㔴挹㑤愹㘲㌶㉥㍦昱㌱愸愶㐱㠴〶㕣㤰㈲㑤㡡㠲换㌶㠹㙢㑥㙣㌷挸敤㈶搵搰㉤㐶户攵㌰㜰㌴愹㡥㐶㡥㈶㜱攵㐸攱㈶㜱㔹㐹㠷㥢挴攵㈷扡㐹㐳㔹㠱慢㐹挷㐳搷㤱㈶慤㠰㕤㠱㈶慤㠴㕡㥡㌴㡣㥢㜷㈲㌸㔷㤳昶㠵㜴换㑤㍡〹㙥摥㈶㥤っ改㝡㙦㤳昶攳愶㡣㘴戶㔵晥〶愳㘸㌰㥡〶㕣ㅣ㈳㑤ㅡ〳㉥摢㈴慥㝦戱攳㐲㙥㌷㘹㉣摤挶搱㡤㙢㔵ㅣ㑤㥡㐰㈳㐷㤳戸㡡愵㜰㤳戸挴愵挳㑤攲㔲ㄸ摤愴㠹慣挰搵愴㡢愰敢㐸㤳㉥㠱㕤㠱㈶㕤ち戵㌴㘹㝦㙥ㅥ㔷搳戸㥡㜴〰愴㕢㙥ㄲ㔷摤㜸㥢㜴㈵愴敢扤㑤㥡捡㑤㤹挶㙣㕣㤶攳㘳㜰㈰つ愶搳㘰㉤っ愴㐹㌳挰㘵㥢挴戵㌸戶ㅢ攴㜶㤳㘶搲㙤ㄶ摤戸㙥挶搱愴㠳㘸攴㘸ㄲ㔷搴ㄴ㙥ㄲ㤷摢㜴戸㐹㕣㤶愳㥢㜴㌰㉢㜰㌵㠹慢㜵㍡搲㈴㉥摢㈹搰㈴㉥攸㤱㈶ㅤ捡捤攳捡ㅥ㔷㤳づ㠷㜴换㑤攲ち㈰㙦㤳敥㠳㜴扤户㐹㐷㜲㔳收㌰ㅢ㤷〸昹ㄸ捣愵㐱㥣〶て挰㐰㥡㤴〰㤷㙤ㄲ搷〵搹㙥㤰摢㑤㑡搲㉤㐵户扦挲挰搱愴㌴㡤ㅣ㑤摡〰㜵攱㈶㜱改㑦㠷㥢昴㈴㡣㜵㤳收戱〲㔷㤳㥥㠲慥㈳㑤攲ㄲ愲〲㑤攲攲㈲㘹㔲㍤㌷㡦慢㡣㕣㑤㕡〰改㤶㥢挴搵㐸摥㈶㜱㐹搲㝡㙦㤳ㅡ戹㈹㑤捣挶攵㑡㍥〶捤㌴㔸㐸〳㉥㘰㤲㈶㉤〲㤷㙤ㄲ搷㈸搹㙥㤰摢㑤㙡愱㕢㉢摤摥㠱㠱愳㐹㡢㘹攴㘸ㄲ㔷ㅡㄵ㙥搲㝢戰攸㜰㤳摥㠷戱㙥搲ㄲ㔶攰㙡搲〷搰㜵愴㐹㕣捥㔴愰㐹ㅦ㐱㉤㑤㕡捡捤晢ㄸ㥣慢㐹换㈱摤㜲㤳㍥㠵㥢户㐹晦〳改㝡㙦㤳㡥攵愶ㅣ挷㙣㕣㍡攵㘳㜰㍣つ㑥愰〱ㄷ㔳㐹㤳㔶㠰换㌶㠹敢愵㙣㌷挸敤㈶慤愴摢㠹㜴晢ㅥ〶㡥㈶㥤㐴㈳㐷㤳戸敡愹㜰㤳㝥㠰㐵㠷㥢昴㈳㡣㜵㤳㑥㘶〵慥㈶㜱㐵㔵㐷㥡挴愵㔵〵㥡昴ぢ搴搲愴㔳戸㜹㕣㝤攵㙡搲㥦㈰摤㜲㤳ㄴ挷昹㐰挲㍤㕢愸ㄸ搲昵㤰收㕣㜱㌸㥤㥢戲㥡搹扡昸ㅢ㥣㐱㠳㌳㘹㔰〲〳㘹搲㔹攰戲㑤敡敡㜰㠳摣㙥搲搹㜴㍢㠷㙥㈱ㄸ㌸㥡㜴ㅥ㡤ㅣ㑤摡ち敡挲㑤摡ㅡㄶㅤ㙥搲㌶㌰搶㑤㍡㥦ㄵ戴㌱㤹㍤ㄱ愵ㄷ㜴ㅤ㘹搲㜶戰㉢搰愴敤愱㤶㈶㕤挸捤敢つ捥搵愴㡢㈱摤㜲㤳晡挰捤摢愴ㅤ㈱昵㘹搲愵摣㤴换㤸㡤㑢捡㝣っ㉥愷挱ㄵ㌴搸〹〶搲愴㉢挱㘵㥢㔴攱㜰㠳摣㙥搲ㅡ扡慤〵㈹摤〳〶ㅤ㕢㕤挴搹㡥㈱挷㤲㉦捥㡤㙤摤㉡㝤攰攲㜸〳㥥挹㌰ㄵ敢て㌲ㄴ晤ㅥ㈶㥦㤶攸㔵㈰戹㝦ち摡晤愸〶㉣㥣㤲㑤㌸散㠸㝥搸戲㕣っ摣戶搶戶戵搲昲户慤ㄲ〹㤶捥昹捦慦扦㜶㉣ぢ㜷㡦慥㑢昸㤷㐷攷捣㈹㉡㘳㑥㌴〹换〱慦㐶挳㌸㘷㥥敢ㄸち㑣挴捥㔹㌴挱㘸摢戴㑦ㅢ攵〴攱挱つ㝣㡡㡢摦㝣㔳昷㝣散㙢㤰㔰㜱㔲戶散戰搷㤲㐳㌰扥㑡挳㤰㙥㜱㉥㉦ㅣ戰ㅡ㡣戳㝡㘷㘴㤶㌵㘰㈶㌵摦昲㙦㙤敡㜷㥣㍡慡搵㈸慦戹愵〴㡢摥㜲晦㤲㙥搶昷㕥㠴敡搶㉢攷㉦ㄷ㡢ㅢ㌵㐳㔰㑤改㘱〰㌸慦㍦㡢㙥挷㤴㍥晣〹㕣㡦ㄲ㝢ㅤ㔰㥦㙣㘹㙥㙤㑥㘷㉡㘶㘰㌵㐰〵晦㤶㌵晥㐴㑦㜸㘴改㈱㠸攸㥢㤳ㅢ㔶搲挴㠷㡦㐸㥢㠲ぢ㥡㥡㡦㙥㤲㙡㑡㕢昹㈷扤〵慦慥㕤㤹㠶慢㐵攴㘷㔷〰ㄷ慡㐴愱晣〹㔵㔹愸〶㙥㐰慣摤㐶㡦ㅡ㍤㝤㑥㌸ㅡ㌳㉢搳戱㠸ㄹ慤慣㠹㈴㙢㔲昱㔴㌸㤲㑣㠵ㄳ㘶㑤扣戶㌶ㅥ慢づ㔵㕢㍥挶㡤昰〹㐵㙣敥㈶㜲㔱㥢愳慥扣〶ㅣㄳ〷㈴搹㝦㤱㠴㘲㠸㡣㕦晣摤㜸攴搹㙡昴愸㌹敥㐷戳〴㙥㠵戸㍢挴㌲户㜹㍡晥㠰㜶攰㌶㐸㝡㐲攲㔸ㅦ㄰慡戵愲ㄸ户㐳㘹昴㐷㍣愳〲㐴つ㠵㥣㐷愴愰㥡〲攸昹㠹㘱慥愰㜱ㄷ捣戰攷慢㝤挰㜲敦㌷敥㠶㐰つ挷㍢㐱晡ㅥ㜲昴攷㙢〴愴摣㍢搵㈴戸㜳㥦㠰戰挸㘰愳搹㔳㌵〱ㄲ昶搵摤㤷㤱㔶愸挰〳戰搳敤㐸㔷搶㐶㙡慢㔲改㘸㙤慣㉡㤲㡡挴敡㤲昱㐸㜵㑤戴慡㉡ㄹ㠹㐶㙡㘳㠹搰㈸㍢晤㍡昸㠴㐶摢㥣戴㘳㡣捤㔱㔷捥㔹戶㥤搳㡥㜱㠸㡣摦㈲㠳敤㌰〸扥㐱扣㐳㥣慥㉢昲㌶㡡〶搱㘲㈰㠸攲㤴㕤つ昰㜰㘰搰づ昰ㄳ㌰㈳挰㤳愰ㄷ㠰晦ち㠱㥡っ㑥〰摥㐰㡥晥㝣㑤㠱㔴〰慥㐳〸㉦挰㌱㕦㠰愷㔹愱〲㝦㐷㈸つ㜰㔵㜵㑤㑤㜵慡慥戶捡㑣挵㈳搱㜴㌸㔱ㄳ㡢挴㉡㉢㉢㙢㉢搳㤱扡捡捡㜸攸㐰㍢晤搳昰〹㑤户㌹〱㜸㠶捤㔱㔷㍥ㄳ㕣攷〰㍣ぢ㤱昱敢〱㜸戶㉤㝦〱昹攵改㌶挶㥥〴攷㘰挸㌵挰㝢扡〰㝥〵㘶〴昸㄰攸〵攰㔷㈱㔰㠷㠱ㄳ㠰㕦㈳㘷〳㝣〴愴〲昰敥扥〰て昴〵㜸㡥ㄵ㉡昰ㄶ㐲㘹㠰愳愹敡㔸慣戲捥㡣㐷愳攱㐸㈴㕡㔳ㄷ慤慥㑢㔷㤹㘶㈴㤲愸慢㠹㐵挳愱戹㜶晡户攱ㄳ㡡摢㥣〰㥣戰㌹敡捡㤳攰㍡〷攰ㄴ㈲攳搷〳㌰愷挹㡡晣〳攴㤷㐷晦ㄸ㕣㡢愴㌸㔵㔶〳扣愳ぢ攰㡦㘱㐶㠰攷㐳㉦〰㝦〲㠱㍡ち㥣〰晣㈹㌹ㅢ攰〶㐸〵攰敤㝤〱摥搶ㄷ攰㈶㉢㔴㘰ㄳ㐲㘹㠰㘳昱捡㜸㌴㥤㑡㔶搵攰愰㔰㤷㡥㠲㑤㤹昱㥡㜸㘵㌴㤹㡥㈵㔲挹㤰㑣㑦攵挶㝤〱㥦搰㐲扢ㄸ〱㜸㤱捤㔱㔷摥〲慥㜳〰㙥㐵㘴晣㝡〰捥搸昲㙦㤰㕦㥥㡢㘴搴ㄲ愰㈵㤰㙢㠰㠳㉥㠰扦㠷ㄹ〱㍥ㅡ㝡〱㜸㌳〴㙡ㄹ㌸〱昸〷㜲㌶挰挷㐰㉡〰〷㝣〱㉥昱〵昸㌸㉢㔴攰㘷㠴搲〰㈷捤㠴ㄹ愹㡡㔵㐶㤲㜵戵㜲〴㡥搷㔶搷搴㥡㜵愹㘴㍣㥤慣慣㡥㠵㘴㙡㈹㌷敥ㄷ昸㠴㑥戰㡢ㄱ㠰㔷搸ㅣ㜵攵㉢挱㜵づ挰㈷㈲㌲㝥㍤〰晦搱㤶㤷㤴㐲㌹㠲ㄶ晢ㄲ㈰㑥㔱搵〰晦昰愳昳ㄸ㕣〶㌳〲扣ち㝡〱㤸て捡㔳愷㠲ㄳ㠰㠳攴攸捦搷㘹㤰ち挰晦㐶〸敦㌱昸ㅢ㐸扤㕦㜲慢慤㔰㠱㥥〸㘵ㅤ㈲㈲㜵搵愹㐸㕤㤵㔹㔳㔵㡤㜳㡥〸㘰慤慤㡢㠶慢慢昰㍣㍣〰㥦〸挹戴㔰㤶㕥づ㥦搰㤹㜶㌱〲戰捣〸戵㜵攵㘷㐳搷㌹〰㥦㠳挸昸昵〰㝣慥㉤摦ㄶ戵挹ㄳ戵㡣㌱〴攷㝣挸㌵挰㥦扡〰摥〱㘶〴昸〲攸〵攰㍥㄰愸㡢挰〹挰㍢㤲愳㍦㕦㤷㐰㉡〰㝦攸ぢ昰〷扥〰㕦㘶㠵ち散㡣㔰ㅡ㘰ㅣ㜱㤳愹㐸㙤戸㌲㙤搶㐵搲㔵戵㠹ㅡ戳慡㌲ㄶ㡤挶慡昰㥤㔷ㅤ㐹㠷㘴㑡㈷㌷慥〲㍥愱㉢散㘲〴㘰㤹捤㘹敢捡搷㐰搷㌹〰慦㐵㘴晣㝡〰扥捡㤶て㐴㙤昲戸㌱㘳ㄲ挱戹〶㜲つ昰㙢㉥㠰昷㠰ㄹ〱扥ㄶ㝡〱㜸㌰〴敡㝡㜰〲昰㥥攴攸捦搷つ㤰ち挰㉦昹〲晣㠲㉦挰㌷㔹愱〲㘱㠴搲〰搷搴㈶㉢〱㙥搲慣慡㑡㐷㤲㤱㜸㙤㍣ㄱ㡤㔵愷㉡挳㘶㙤㕤扣㉡㥡づ摤㙣愷慦㠴㑦攸ㄶ㥢ㄳ㠰㘵㈶㈶㌷㥣扡昲摢愰敢ㅣ㠰㌹㝦ㄳ扦ㅥ㠰敦戰攵㌱攴㤷㘷戱ㄹ搳〸捥㥤㤰㙢㠰㌷戸〰摥〷㘶〴昸㉥攸〵攰㘱㄰愸㝢挰〹挰挳挹搱㥦慦晢㈰ㄵ㠰搷晢〲摣收ぢ昰〳㔶愸挰㐸㠴戲昶攰㐸㉡㥡慣㡥㐶㤲㐹㌳ㅡ㠹㈵㜱ㄶ㥣愸㌵慢愲㜵㌵㤱慡戰㔹㔹ㄹづ慤戳搳㡦㠲㑦攸㐱㥢ㄳ㠰㘵ㄶ㈵㌷㥣扡昲㠷愱敢ㅣ㠰㌹昷ㄲ扦ㅥ㠰ㅦ戵攵ㄳ㤰㕦ㅥ㔴㘷捣㈶㌸㡦㐱慥〱扥挷〵昰㘴㤸ㄱ攰昵搰ぢ挰〷㐰愰㥥〰㈷〰㑦㈱㐷㝦扥㌶㐰㉡〰晦挵ㄷ攰摢㝤〱㝥搲ちㄵ㤸㡥㔰ㅡ㘰ㅣち慡敢ㄲ改㘸慡〶㕦㜲㠹㜰㕤㈲㕣㠹昳㠹㜴㜵㌴ㄱぢ㠷敢挲㤵㈱㤹〶挹㡤㥢〱㥦搰摦敤㘲〴攰愷㙤㡥扡昲㡤攰㍡〷㘰捥㥢挴慦〷攰㘷㙤昹㈱挸㉦㑦昱㌳づ㈷㌸捦㐳慥〱扥搶〵昰ㄱ㌰㈳挰㉦㐰㉦〰ㅦ〹㠱㝡〹㥣〰㍣㠷ㅣ晤昹㝡〵㔲〱㜸慤㉦挰㔷晡〲晣㥡ㄵ㉡㤰㐴㈸つ㜰㕤㉡㕤ㄵ㡥㠵ㄳ愹㔴戸㉡㤲慥㠹搵㥡㜸㕢㤹㑥挴攲搱摡㙡㝣摤㠵㕥户搳愷攰ㄳ㝡挳收〴攰㌷㙤㡥扡昲户挰㜵づ挰㥣昳㠸㕦て挰晦戰攵㐷㈱扦㤱愴㐵㠲攰扣ぢ戹〶昸㍣ㄷ挰㝣〶㉦〱㝥て㝡〱戸ㄹ〲昵〱㌸〱㜸㈱㌹晡昳昵㈱愴〲昰㔹扥〰㥦攱ぢ昰挷㔶愸㐰〶愱㌴挰㘱散愷戱㔸㕤扣㌲㡣愱㜱戲㈶㥣㠸㠷挳戵㌱戳㍡㤹㑣愴敢愲昱㜸㐸愶ㅦ戲昴挵昰〹㝤㙡ㄷ㈳〰换捣㐳㕢㔷晥ㄹ㜴㥤〳昰攷㠸㡣㕦て挰㥢㙣昹㌱愸㑤㥥晦㘸捣㈷㌸㕦㐲慥〱㍥搱〵昰〹㌰㈳挰㥣㝤㈸〰慦㠰㐰㝤つ㑥〰㕥㐹㡥晥㝣㝤〳愹〰㝣扣㉦挰挷晡〲晣㙦㉢㔴攰㘴㠴戲づㄱ㐹戳戶㌶㡡㐱㜱㙤㈵捥搶挲改㜸戵㔹ㄵ慢愹慡っ攳慣愲㉡ㅡ㑥㠴扥戳搳慦㠲㑦攸㝢㥢ㄳ㠰㌷摢ㅣ㜵攵㍦㠰敢ㅣ㠰㝦㐴㘴晣㝡〰晥㡦㉤㕦㡤晣昲㜰㑣愳㠹攰晣っ戹〶㜸㤱ぢ攰戳㘱㐶㠰㌹㜳㔰〰㍥〷〲昹㠳㔸〲昰戹挲㔹〰ㄷ攳搴㕥〰㙥昴〵㜸㠱㉦挰㈵㜰㘲愸挰㠵〸愵〱慥愹㡥㔵〳捤㜸〲㡦ㄳ㡣㔴㐷慢ㄲ挹㐴㕤慡㈶㥣挲㜸〳扢㜱㜵㍣㔴㙡昹ㄸㄷ挱㈷ㄴ戰㌹〱戸慢捤㔱㔷㕥〶慥㜳〰㌶㄰搹て攰愰㉤扦〲昹攵挹愱㐶㠶〰㜷㠷㕣〳㍣搷〵昰㔵㌰㈳挰㍤愰ㄷ㠰慦㠶㐰㤵㠳ㄳ㠰慦㈱㐷㝦扥戶㠲㔴〰㍥摣ㄷ攰㐳㝤〱摥挶ちㄵ昸㌳㐲㘹㠰慢慡㤳㔵攱扡㙡㌳㔶ㄷ㑢㐵慡敡慡昱㕦㑤愲㈶㕡ㄷ㡦挶搲攱㐸㙤㑤愸㤷㥤晥〶昸㠴戶戵㌹〱㜸㍢㥢愳慥㝣㝢㜰㥤〳㜰㙦㐴昶〳㤸搳晥㐴㝥ㅢ昲换㘳㔵㡤攵〴㠷㔳晦㌴挰㔳㕤〰摦〹㌳〲摣ㄷ㝡〱昸㉥〸㔴㍦㜰〲昰摤攴㙣㠰㉢㈰ㄵ㠰昷昷〵㜸愲㉦挰扢㔸愱〲昷㈳㤴〶ㄸㄷ㡣㙢搳攱㘴㘵ㄸ攰㘲ㄸ㔷㥢愸㑣㈴㜰挹㌲ㅥ挳㘵㠹㜰㈲㔲ㅤ㤲改㜶挸㙡㍣〰㥦搰〰扢ㄸ〱㜸㌷㥢愳慥㝣㈰戸捥〱㜸㄰㈲晢〱扣扢㉤㝦ㄴ昹㡤㤵慣㜲〵〱摡〳㜲つ昰扥㉥㠰ㅦ㠷ㄹ〱ㅥっ扤〰晣〴〴㙡㉦㜰〲昰㕦挹搱㥦慦扤㈱ㄵ㠰㠷晡〲㕣敢ぢ㜰愵ㄵ㉡昰ㄴ㐲㘹㠰㜱搸㑤攱摢っ㐷㠵㜰㌴ㄲ㡥搵搶攲㐱昰搵㘶㕤㡤㠹换挴改㜸搸っ挹㔴㌹㘴㌴晥づ㥦㔰戵㕤㡣〰ㅣ戱㌹敡捡愳攰㍡〷攰ㅡ㐴昶〳㌸㘶换㥦㐷㝥㜹㈰慦戱㡡攰㜰捡㥤〶㜸㉦ㄷ挰㉦挳㡣〰て㠵㕥〰㝥〵〲㌵っ㥣〰晣㉡㌹ㅢ攰㝤㈱ㄵ㠰晦攰ぢ昰㈰㕦㠰昷戳㐲〵摥㐴㈸つ㜰㜵扣愶㉡㔶㥢っ㔷㐵愳挹㐸㤵㤹慥㑢搵搶愶㙡昰攰㌴㕣挶っ搷㐴㈳㈱㤹收㐶㠰摦㠲㑦㘸㤴㕤㡣〰㉣㌳摣㙣㕤昹ㄸ攸㍡〷攰戱㠸散〷昰㌸㕢晥㍥㙡㤳愷ㄵㅢ慢〹搰〴挸㌵挰㝤㕤〰㝦〴㌳〲㍣ㄱ㝡〱昸㘳〸搴晥攰〴攰㑦挸搹〰ㅦ〰愹〰摣摢ㄷ攰敤㝣〱㥥㙡㠵ち㝣㡥㔰ㅡ㘰㌳㤶㌲㜱㙥ㄶ㑢㔶愶㘲㌸㡢愸挴㄰㉥ㅣ㡥㔴㔶攱㥡愵㝣晤㠵㘴㡡ㅡ㐱摣〴㥦搰㠱㜶㌱〲戰捣㑥戳㜵攵㌳愰敢ㅣ㠰㘷㈲戲ㅦ挰戳㙣昹扦㔰㥢㍣捡搹㌸㤷〰ㅤ〴戹〶戸㥢ぢ攰敦㘰㐶㠰て㠶㕥〰晥ㅥ〲㜵㈸㌸〱㜸㌳㌹ㅢ攰挳㈱ㄵ㠰扢晡〲㕣敡ぢ昰㤱㔶愸挰㑦〸㘵ㅤ㠳㙢㔳挹㐸〴ㄷ㈲㙡攲戸㜵ㄷ愹㡢挷捣㜸㙤㑤つ敥改㘱摦慥㐹㈵㐲㌲扤㡣㈰晥っ㥦搰㕣扢ㄸ〱㔸㘶㤶搹扡昲〴㜴㥤〳㌰攷愳昹〱㥣戲攵㕤㜰搷㔰㥥㜳㙤㕣㑣㠰搲㤰㙢㠰㝦晣挱㜹戹戲㉢捣〸昰㍣攸〵攰㌲〸㔴㍤㌸〱搸㈰㘷〳扣〰㔲〱昸㍢㠴昰㕥慥晣ㄶ㔲敦攵捡㐶㉢㔴愰〷㐲㔹㠷㠸㐴㉤扥搲捣愸㔹㠳换㄰㤱㜸㜵㙤㘵〲㐳攵㑡ㅣ㠲㙢昰搵㠷㉦㌹㤹ㅡ㐶㄰㝢挲㈷搴㙣ㄷ㈳〰换慣㌰㕢㔷扥〸扡捥〱㤸㜳挹晣〰㙥戵攵扤㔰㥢㍣〴摣戸㤲〰㉤㠶㕣〳晣㍦㉥㠰㝢挳㡣〰㉦㠱㕥〰摥〱〲戵ㄴ㥣〰摣㠷㥣つ昰㜲㐸〵攰㡦㝣〱晥㝦扥〰ㅦ㙢㠵ち昴㐳㈸つ㜰㘵㑤慣慡㉥ㄲ慦挲〵昶慡〸敦挵㠵㔳㜵㌱っ敡ㄲ戸㌴㕣㕤㕤㘵㠶㘴㕡ㄷ㐱摣ㄹ㍥愱攳敤㘲〴㘰㤹搱㘵敢捡㔷㐰搷㌹〰㜳ㅥ㤸ㅦ挰㈷摡昲摤㔰㥢㜱ㅤ㉢戹㤶〰㥤〴戹〶昸㜵ㄷ挰㝦㠰ㄹ〱㍥ㄹ㝡〱㜸て〸搴㈹攰〴攰挱攴攸捦搷㥦㈰ㄵ㠰㕦昶〵昸㐵㕦㠰㑦户㐲〵昶㐶㈸つ㜰愴愶㈶㡥㐳㜰㜵ㄲ㤷㈹㈳ㄱㅣ㈲㙡㜰ㄲ㕣㕢㔳㕢㥤㑣搵㔵搵㈶㘳愱搵㜶晡㌰㝣㐲㘷搸㥣〰㉣戳戱戸㔹搴㤵㥦〵㕤攷〰捣㌹㕣㝥〰㥦㘳换㙢㤰㕦ㅥㅦ㙦摣㐴㜰捥㠳㕣〳晣㌷ㄷ挰㐳㘱㐶㠰捦㠷㕥〰摥〷〲㜵㈱㌸〱㜸ㄸ㌹ㅢ攰㡢㈱ㄵ㠰ㅦ昷〵昸㌱㕦㠰㉦戵㐲〵昶㐳㈸敢㄰㠱晤㌵㕥㔹ㄷ㡢㈶攲搵ㄱ㕣晦慤挳昱㈲ㅤ㡢挷ㄳ㤵㈶慥〹㐷㤲㈱㤹㑥㐵㄰㐷挲㈷㜴戹㕤㡣〰㉣㌳愹㙣㕤昹㤵搰㜵づ挰㥣㝦攵〷昰㕡㕢㍥ㅥ戵ㄹ晣愳攲〶晦㙣戹扡摡慥㜲ㄲ攴㜴攴㑢挹昴ㅣ摡㔴㤲戵㝥㐲搷挲ㄶ扦㜸㌶ぢ㙣㝢㜴㈹扤ㄱ㡣敦摦㌸搵㌳㌷㘶攰㉦搷㤹㐳㐶㡦㡡つㄹ扢㌴㘹㌶昰㙦挹㘲摡〶㕣㡢戶㙤㥣搸㡡户㜸愰昳捣收㤱昲㔷㑥㌹㜵㘷㉢㝢㘶挷㘰晢㘱搲扢戵㑢散㍦㈴㙣扢㑤㙤挹晡攱搹挸㤸搰〴挵㘰㍥㝡㝡摢㜶捥昱㔴攴ㅤ摢愵昸㡢搱昸㕢戶㘶捡㡥搸㡡搹㝣㈵挵㕤搴ㅥ㝥㝦〹摢㝡昲㉦ㅥ戶㙢〷ㄸ摢戴戸㜱㘷㙣挳㡥㍥㝦㌶㙦㔴㝤㐶愶㌹昵㠵㕥ㄹ㌷〰㥥挰ㄴ㙣㙦改昰〱愳〶挴㑡晦㠲ㅤ敤㝦㤱㠴晢㙦晢扣㈲愶攴㑦搰㤸㠶㠸㡡晢ㄴ攳㔱愴㙥〷㌳〰㙦㜲㥦㜷㝢ぢっ摥挲ㅦ㝦昷㍣〸昸㘶㑢攱㜹㄰昰㕤㠸㈴ㅦ愰搹㐸㤲摤ㅢ敥戶愵慥扤攱ㅥ㐸昱㕢㘴ㅣっ摢ㅥ㕤搴㍡㌰摣㈳㤴挱㤹㉥㠱㐳昵㠶㡦ㅢ㔰慢慥㐳㍡扢搸愰㜱㌸敢㙦㠳挹〰㥦㤲搷收㉢㜹㡤愵昰㍣愲昷〹愶㘴愴㠴戳攴扦摡㔲㔷挹ㅢ㈰挵㉦㈶捤敢㤲㥦〶愳㑢晥㍢摥〵戸㙦㑡慦㙡搴㈵慥㤲攷戳攴ㄷ㘰㌲挰愷攴昳昳㤵㝣㥥愵昰㍣㍣昷ㄵ㐴㤲㤲㥢㥣㈵扦㙡㑢㕤㈵扦〶㈹㝥㌱昳㕣㤷晣㌶ㄸ㕤㌲㘷㘳〴㕡㜴挹㘳〶㐴搵ㄹ慥㤲㌳㉣昹〳㤸っ昰㈹昹搴㝣㈵㥦㘲㈹㍣㡦戵晤ㄸ㤱愴攴攵捥㤲㍦戱愵慥㤲㍦㠵ㄴ扦㜸㌴㡦㉥昹ぢ㌰扡㘴捥㙦〸ㅣ慦㑢ㅥ㍦愰㐶慤㜴㤵扣㠲㈵㝦〳㤳〱㍥㈵ㅦ㥢慦攴㘳㉣㠵攷㠱戳摦㈳㤲㤴扣捡㔹昲㘶㕢敡㉡㤹㔳っ昰㡢㠷㘲敡㤲㝦〱愳㑢收㡣㠱挰㘹扡攴㜱㐰㜹戱慢攴搵㉣㤹㌷攱〷昸㤴扣㌰㕦挹捤㤶挲昳㈸㔸摥愷㤷㤲捦㜵㤶㉣㌷敢ㄹ摦㔵㜲㄰戶㔲昲昹扡㘴摥㐵搷㈵昳ㅥ㝣攰㐲㕤昲搸〱㌱㔵敦㉡昹㘲㤶捣摢摡㝥㈵愷昲㤵㥣戴ㄴ㥥㠷戴昲捥户㤴㝣愵戳㘴戹晤敤㈹㤹户挱愵攴戵扡㘴摥㤷搶㈵昳慥㜶攰㙡㕤昲㐸ㅣ㌱㡥㜰㤵㝣㉤㑢收㡤㘲扦㤲て捥㔷昲㐱㤶挲昳昸搴㍤㄰㐹㑡扥挹㔹戲摣㔰昶㤴扣㈷㙣愵攴㕢㜴挹扣㥢慢㑢收㝤攲挰㙤扡攴戱搸㌱づ㜴㤵㝣〷㑢收慤㔷扦㤲㈷攷㉢㜹㝦㑢攱㜹戰㈹敦捥㑡挹昷㍡㑢㤶㕢戴㥥㤲㜹慢㔶㑡扥㕦㤷捣晢愳扡㘴摥㜹つ慣搳㈵㡦挴㡥㌱搶㔵昲㐳㉣㤹㌷㌳晤㑡摥㉦㕦挹㈳㉣㠵攷㤱愳㤳ㄱ㐹㑡㕥敦㉣㔹㙥㝡㝡㑡收捤㑦㈹昹〹㕤㌲敦㌸敡㤲㜹㉦㌳戰㐱㤷㍣ㅡ㐷㡣㍡㔷挹㑦戲㘴摥ㅥ昴㉢㌹㤲慦攴㙡㑢攱㜹ㄸ㈸敦㈰㑡挹捦㍡㑢㤶摢㠸㥥㤲㜹㍢㔱㑡㝥㕥㤷捣㝢㜸扡㘴摥ㅤっ扣愸㑢ㅥ㡢㤲昷㜲㤵晣㌲㑢㍥ち㈶㝥㈵敦㥥慦攴㐱㤶挲昳㤸㑥摥㤳㤳㤲摦㜴㤶㉣㌷收㍣㈵昳〶㥤㤴晣戶㉥㤹㜷捣㜴挹扣摦ㄶ㜸㐷㤷㍣ㅡㅦ扦晥慥㤲摦㘳挹扣㠵攵㔷㜲摦㝣㈵敦㘸㈹㍣て搰攴㕤㉥㈹昹㘳㘷挹㜲慢换㔳㌲㙦㜹㐹挹㥦敡㤲㜹㥦㐹㤷捣㍢㔸㠱捦㜴挹㘳㔱昲戶慥㤲㌷戱攴搵㌰昱㉢㌹㤴慦攴㜲㑢攱㜹戴㈵敦ㅢ㐹挹晦㜲㤶慣㙦ㅥ攵ㅥ㤷㜹ㄳ㐹㑡晥㔶㤷捣㍢㌷扡㘴摥ㄳち㝣愷㑢ㅥ㠳㡦㥦攱㉡㜹㌳㑢收㙤ㄶ扦㤲㑢昲㤵摣挵㔲㜸ㅥ㍡挹㍢㌱㔲昲㉦捥㤲攵㜶㡣〷㘵摥㤶㤱㤲㡢戰ㄲ〳㘷㜲扣ㄷ愲㑢收㕤㤶㐰㌱愴㌸㉤ㅡ㠷㤲㝦摥散㍣㤳㉢㠱㐲昱挶㠵㕦挹㥢㘱敡㝢昲昹扤愵昰㍣づ㤲昷㌶愴攴㈰攲㘶㑦㍥攵〶㠷愷㘴摥攸㤰㤲扢敢㤲㜹㜷㐱㤷捣晢ㄶ㠱㥥扡攴㌱搸㌱扥㜶㤵ㅣ㘲挹扣ㄵ攰㔷昲愶㝣㈵㝦㙥㈹㍣て㙡攴摤〲㈹㜹㍢㘷挹㜲换挰㔳㌲㙦ㅤ㐸挹扤㜵挹扣㕥慦㑢收㥤㠰㐰ㅦ㕤昲㜸愰晣㤱慢攴扥㉣㤹ㄷ搷晤㑡㝥㉦㕦挹敦㕡ち捦㈳ㄴ㜹晤㕤㑡摥挵㔹戲㕣㠴昷㤴捣㡢昱㔲昲〰㕤㌲慦㡥敢㤲㜹㙤㍤㌰搰㉥㌹慡摥㜰㤵扣㍢㑢收攵㙡扦㤲㕦捥㔷昲㑢㤶挲昳㜰㐳㕥搱㤶㤲㠷㌸㑢㤶换摡㥥㤲㜹㜹㕢㑡づ敢㤲㌷㠱搷㈵昳㙡㜵愰㑡㤷㍣づ挷攵㘷㕣㈵㐷㔸㌲㉦〰晢㤵晣㘴扥㤲晦㘶㈹㍣㡦ㅤ攴㌵㘲㈹㜹愸戳㘴戹㔰散㈹㤹ㄷ㡣愵攴㘱扡㘴㕥挱搵㈵昳晡㙦㘰㕦㕤昲ㄸ㤴晣㤸慢攴晤㔸㌲㉦愹晡㤵晣㔰扥㤲ㅦ戴ㄴ㥥〷〲昲慡慢㤴㍣捥㔹㜲㤹㉤㜵㥤㝣昲ㄲ慣㤴㍣㐱㤷摣ㄳ扣㉥㤹㔷㔴〳㤳㜴挹攳昱昱扢挷㔵昲㘴㤶摣ぢ㈶㝥㈵摦㤱慦攴摢㉤㠵攷㔱㝤扤ㄱ㐹㑡㥥敥㉣㔹㉥㘶㝡㔰敥〳㕢㈹㜹愶㉥㤹㔷ㄹ㜵挹晤昰㉥㌰㕢㤷㍣ㄲ㈸摦攸㉡昹㘰㤶捣换㝥㝥㈵㕦㥢慦攴㙢㉣㠵攷㈱㝡扣㌲㈸㈵ㅦ改㉣㜹て㕢敡㐲㤹㤷〹愵攴戹扡攴㌰㜸㕤㌲慦晡〵ㄲ扡攴搱㌸㘲㕣攱㉡㌹挵㤲㙢㘰攲㔷昲挵昹㑡扥挸㔲㜸ㅥ㙦㌷ㄴ㤱愴攴愳㥣㈵换〵㌷て捡挳㘰㉢㈵㌷攸㤲㜹㈵㑣㤷捣敢㘸㠱㈶㕤昲㈸散ㄸ攷戸㑡㕥挸㤲㜹㘹捡慦攴搵昹㑡㍥摤㔲攴㍥㜸㉥㌴挹㉥㘳〹攲ㅡ㐷㤳㉣〵〹㤶昲捡㤵敦㌵ㄸ㜹ㄲ捣㄰晤挸っ慣搲㌲㕢㐵㔰㡥つ㉣㑤昳攲㔴户㌴ㄷ㙦㤹昲摣づ㜹摡㔸挳㘸慥㉣敢㡥愷㘷戴㉣㌰㕢㈶攳㘱㌰㜸㘶挶㡣晡㐶㙢搵ㄲㅥㄲ挳愷ㄸ搸捦㘷㌰㠴攳慡挰㐰㝡㙡ぢㅥ搸搰㌵㍤戱ㄵ㡦㥣㐹㤵㌵㑥㡢㘷㌲㘶㑢搳敦㘱㜵㈳愶挲昰て㤴攱㐷㍦㔴挳㜷㠵ㅡ㤷㥥攵㍥捦挱昱㕣㥤㜶㍣散攷㉡ㄵ昳愱ㅢ扦㙤㙤愳㉣戶㉤㔶慢搰㘷戹㡢昳㜹搵づ㜲挹ぢて昲挰㙣〹㜶㔴㐹扤㜸愴㥣㜱㉣扢摣㠶攲㠴ㄴ㤵㑣㐳慢ぢ㕤愴攳ㄹ㐶搷挶㌹昱㤶㤶昸戲戲挶㌹つ㘶搳扣捣晣戲㌹㑢㜰㔵ㄲて昰㐱戰戲戲㌲攳㜸晣捦っ㝣㠵㘶摢㝢搵〹㑣戵㠲㘴㈵㐸㔰ㅤっ〵昷㉣慢摣攳㝣换㍤㐹㑣戳攵㥥㑣昷㌶㠴搵攵慡挳攱捦㤲㡤㔳愰挸愶攴㐵㉤昹㍣㥤㑡昳㍦㤱㥣〶ㄲ㔴扣㠲攵㐸㤹昱㑤㜹㠶㤸㘶㔳㥥㐹㜷㐷捡昹㜶捡戳愱挸愶攴㐵㈹㐹㜹づ捤捦㈵㌹て㈴愸ㄶ扡㔳㉥昰㑤㜹愱㤸㘶㔳㕥㐴㜷㐷捡㡣㥤昲ㄲ㈸戲㈹㤷摢㈹㉦愵昹㘵㈴㤷㠳〴搵戱敥㤴〹摦㤴㙢挴㌴㥢㜲㉤摤ㅤ㈹㜹㔹㐹㠰扤ㅡ㡡㙣㑡㕥ㄴ㤲慤扣㠶收搷㤲㕣〷ㄲ㔴愷扡㔳ㅥ攲㥢昲〶㌱捤愶扣㤱敥㡥㤴慢敤㤴㌷㐳㤱㑤挹㡢㍡㤲昲ㄶ㥡摦㑡㜲ㅢ㐸㔰㥤敦㑥㌹捤㌷攵㕦挴㌴㥢昲㑥扡㍢㔲㕥㙣愷扣ㅢ㡡㙣㑡㕥㤴㤱㤴昷搰晣㕥㤲晢㐰㠲㡡㔷㘰ㅣ扢捦㜸摦㤴敢挴㌴㥢昲㐱扡㍢㔲昲戲㡣〰晢㌰ㄴ搹㤴扣愸㈲㈹ㅦ愱昹愳攲〳ㄲ㔴户戸㔳敥敢㥢昲㜱㌱捤愶㝣㐲摣㡢慣扣㐵敡づ㍢攵〶㈸戲㈹㜹㔱㐴㔲晥㡤收㑦㤲㍣〵ㄲ㔴昷扢㔳㐶㝤㔳㙥ㄴ搳㙣捡㘷攸敥搸捡㠷散㤴捦㐱㤱㑤挹㡢ㅡ㤲昲㜹㥡扦㐰昲㈲㐸㔰昱ち㠶〳搸㍤㝤㔳扥㈲愶搹㤴慦搲摤㤱昲㐹㍢攵敢㔰㘴㔳昲愲㠴愴㝣㠳收㙦㤲扣〵ㄲ㔴捦扢㔳敥敡㥢昲ㅤ㌱捤愶㝣㤷敥㡥㤴㉦摢㈹摦㠷㈲㥢㤲ㄷㄵ㈴攵〷㌴晦㝦㈴ㅦ㠲〴搵摢敥㤴㝤㝣㔳㝥㈲愶搹㤴㥦搲摤㤱㤲㤷ㄵ㘴昷昹っ㡡㙣㑡㕥ㄴ㤰㤴㥦搳㝣ㄳ挹ㄷ㈰㐱昵愹㍢攵㔶扥㈹扦ㄲ搳㙣捡慦改敥㐸戹挹㑥昹つㄴ搹㤴ㅣ搴㑢捡㙦㘹晥㙦㤲敦㐰㠲敡㕢㜷捡㌲摦㤴㍦㠸㘹㌶攵㡦㜴㜷愴摣㙣愷晣〹㡡㙣㑡づ捡㈵攵捦㌴晦㠵攴㔷㄰㍣㡦〴搴戱晢晣晡扤摦ㄷ㕦㜱ㄹ㑤戳㈹扢㠰㜵愶㉣㐱っ〱戶ㄴ㡡㙣捡㈰愴㤲㌲㐰昳慥㈴㘵㈰㐱搵摤㥤昲㍢摦㤴摤挴㌴㥢戲㍢摤ㅤ㕢ㄹ戲㔳昶㠴㈲㥢㜲㍢㍢㘵㌹捤㐳㈴㕢㠱〴ㄵ㐷挰㡥慤晣挲㌷㘵㉦㌱捤愶摣㤶敥㡥㤴㝤敤㤴摢㐳㤱㑤挹㐱慤㙣㘵㙦㥡敦㐰搲〷㈴愸〶戸㔳㝥攸㥢㜲㈷㌱捤愶散㐷㜷㐷捡摤敤㤴ㄵ㔰㘴㔳づ戱㔳昶愷昹㉥㈴扢㠲〴㔵搸㥤昲㉤摦㤴〳挵㌴㥢㜲㄰摤ㅤ㈹㌹㉣㤵㕥晥〱㡡㙣捡愱㜶捡㍤㘸㍥㤸㘴㑦㤰愰ㅡ收㑥昹愲㙦捡扤挵㌴㥢㌲㑣㜷㐷捡晤散㤴㔵㔰㘴㔳㜲㔰㈸挰㔶搳㍣㐲ㄲ〵〹慡〹敥㤴㑦昹愶慣ㄵ搳㙣捡㍡扡㍢㔲㑥戶㔳敥〳㐵㌶㈵〷㜵㤲㜲ㄸ捤㠷㤳散ぢㄲ㔴ㅣ挱㌹㜶㥦㌶摦㤴㈳挵㌴㥢㜲ㄴ摤ㅤ㈹㌹慣ㄳ㘰挷㐰㤱㑤㜹愴㥤㜲㉣捤挷㤱㡣〷〹慡戹敥㤴昷昹愶㥣㈴愶搹㤴晢搳摤㤱㌲㘵愷㍣〰㡡㙣㑡づ慡㘴㉢愷搰㝣㉡挹㌴㤰愰㙡㜰愷扣捤㌷攵っ㌱捤愶㥣㐹㜷㐷捡㠵㜶捡搹㔰搸㈹㑢㤷㐰扡㡦摦摤㙥㍤〸㜲晣㌹㠵挱昸㡢ㅦ㜸慡愵㤹挲㌸㘶㈱敥㥡㉦ㅢ摢㤴㘹㔹挶㐰㕤昰㥣戹㔲戹㈷㕥㔲㍣昴户挵攲㘸㘸㈷㠴攲慢昴㐶㙣摥晦㈱づ挷愷敤㌷换ㄹ㜱ㄸ㕥㘵挵〱挵挱ㅦ㌷㔸摤㠰っ捣㌲㕣ㄴ㑡㜱㐰㈸㡡㍦㕢㡡ㄱ㔰ㄸ㠷〲愸㔲㡥㉣㍡㍣挴㘱敡摦昸㔷㔰づ㐳㌲㜵㉣㡢㘳敡挳挹攱つ㕦攵挷㕢搲㌲づ㔳搴〹㜶慤搷㔸戵摡㕢户挲㔶㕣㥤戳㜵ㅣ㤸挸搶㕤攵摣扡戹㑣㜱ㄲ㔴摣㐲㈳㑥㡥攳㄰㐹㥦㜰愶攷㈰㠴㔲㥤晥㔴㜰ㄲ散㡡㥣昴ㅣ㤰㠸攲昲㥣昴ㅣ愴㠸攲㌲㘷晡㌴㔳㜰㔰㈲改攷㤱攳㤸㐴搲捦㜷愶㍦摢㤲敡昴ㅣ㠸㐸戰㡢㜲搲㜳㜰㈲㡡ぢ㜳搲㜳挰㈲㡡ぢ㥣改ㅢ㤸攲㐲愸㈴㝤㈳㌹㡥㑦㈴㝤㤳㌳㍤〷㈷敤㕢㝦愹ㅤ散㥣㥣昴㤷搹㡡戳㜳搲㕦㙥㉢捥㜲愶㙦㘱㡡㌵㔰㐹晡㔶㜲㙢挱㐹晡㡣㌳㍤〷㉡敤改㌹㐰㤱㙤㌹㍤㈷晤戵戶攲戴㥣昴ㅣ挸㠸挷㥦㥣改㤷㌲挵つ㔰㐹晡㘵攴㌸㙥㤱昴换㥤改㌹㘸㘹㑦㝦㡢ㅤ散攴㥣昴ㅣ挰㐸㤶㤳㜲搲㜳㔰㈳㡡㍦㍡搳ㅦ捦ㄴㅣ挴㐸晡ㄳ挸㜱っ㈳改㔷㌸搳㜳〰搳㥥㥥〳ㄷ〹㜶㐲㑥晡㝢㙤挵昱㌹改㌹挰ㄱ㡦攳㥣改㑦㘲㡡㜵㔰㐹晡㤳挹㍤〸㑥搲慦㜲愶攷㘰愶㍤晤㈳㜶戰㘵㌹改ㅦ戵ㄵ㑢㜳搲户搹㡡愳㥤改㑦㘳ちづ㙥㈴晤改攴㥥〰㈷改㔷㍢搳㜳㘰搳㥥㥥〳ㅡ搹㤶搶㥣昴㑦摡㡡㤶㥣昴ㅣ昸㠸挷㈲㘷晡戳㤹㘲㈳㔴㤲晥ㅣ㜲ㅣ攷㐸晡㜳㥤改㌹挸㘹㑦晦扣ㅤ慣㌱㈷㍤〷㍣㤲愵㈱㈷㍤〷㐱愲㔸攰㑣㝦㈱㔳㜰搰㈳改㉦㈲昷㉡㌸㐹㝦戱㌳㍤〷㍣敤改㌹搰㤱㘰昳㜲搲扦㘹㉢搲㌹改摦戲ㄵ愶㌳晤攵㑣昱づ㔴㤲晥ち㜲敦㠲㤳昴㔷㍡搳㜳昰搳㥥㥥㠳ㅥ㐹ㅦ捦㐹捦㠱㤰㈸收收愴晦搰㔶捣㜱愶扦㥡㈹㌸ㄸ㤲昴搷㤰晢ㄴ㥣愴扦搶㤹㥥〳愱昶昴ㅣ〰㐹㤶挳㜲搲㙦戲ㄵ㠷收愴攷㐰㐹㍣づ㜱愶扦㠱㈹扥㠲㑡搲摦㐸㡥攳㈲㐹㝦㤳㌳㍤〷㐵敤改㌹ㄸ㤲㘰戳㜲搲㜳㠰㈴㡡㤹㌹改扦戳ㄵ㌳㥣改㙦㘳ちづ㤲㈴晤敤攴㝥〴㈷改敦㜰愶晦挹㤲敡㘳㍥〷㐶㤲㘵㙡㑥晡㕦㙣挵㤴㥣昴扦摡㡡〳㥣改敦㘶㡡㘲㄰㐹㝦て㌹㡥㤷㈴晤扤搶ㅢ㌲攵ㅣ㉣戵㙦㝤〰㥣愴㥦㤸㤳㥥〳㈷㔱㑣挸㐹捦挱㤴㈸挶㍢搳慦㘳㔴づ㥥㈴晤㠳攴㌸㜶㤲昴て㔹㙦㈴㍤〷㑥敤改㌹㘰㤲㘰愳㜳搲㠷㙣挵愸㥣昴ㅣ㔸㠹挷㐸㘷晡㌶㐶敤〵㈲改ㅦ㈳挷㜱㤴愴㕦㙦扤㤱昴ㅣ㐴戵愷攷攰㐹㠲つ捦㐹捦〱㤵㈸㠶攵愴攷㈰㑢ㄴ晢㌸搳㙦㘰㔴づ慡㈴晤摦挸㜱㑣㈵改㥦戴摥㐸㝡づ愸摡搳㜳㈰㈵挱㘲㌹改㜷戱ㄵ㌵㌹改㌹攰ㄲ㡦愸㌳晤㐶㐶ㅤ〸㈲改㥦㈱㌷㠸〴敤㌶㥥戵摥㐸㝡づ慥摡搳㜳㔰㈵挱㉡㜳搲㜳愰㈵㡡㜰㑥晡㍤㙤挵摥捥昴㉦㌲㉡〷㕢㤲晥㈵㜲㘱ㄲ愶㝦搹㝡㈳改㌹搰㙡㑦捦〱㤶㘴ㄹ㥣㤳㍥㘲㉢昶挸㐹捦㠱㤸㜸晣挱㤹晥㜵㐶慤〵㤱昴㙦㤰攳戸㑢搲扦㘹扤㤱昴ㅣ㜴戵愷攷㘰㑢㠲敤㤶㤳㥥〳㌰㔱っ挸㐹捦㐱㤹㈸㜶㜵愶㝦㠷㔱㌹〸㤳昴敦㤲ㅢ㐵挲慤㝦捦㝡㈳改㌹〰㙢㑦捦㠱㤷〴摢㌹㈷晤㌸㕢搱㉦㈷晤㜸㕢戱㤳㌳晤㠷㡣捡〱㤹愴晦㠸ㅣ挷㘳㤲晥㘳敢㡤愴攷㘰慣㍤晤ㄴ㜰㤲㝥㠷㥣昴ㅣ㤸㠹愲㜷㑥晡㘹戶㘲㝢㘷晡捦ㄸ㤵㠳㌳㐹晦㌹戹㤹㈴摣晡㑤搶ㅢ㐹捦㠱㔹㌶㝤昹愱攰づ㠲㑤昱㔲㤵㥣㥢㥡㍢㜷㜳㜹㐹㐵㥦㤲㠳昷敢㝥挹㝢㝦晦攰摣㤷てㅦ晥挹㑦㤷㕦晥昲㠷攷㙥晣改愱挴昰扦㕤㝤昵ㄳ㤳搶㙣晣㘰敢昴摡攲㝢㌷㑦㕥㝢㙣攵㠲㘳ㄷ愵㘷敤㌱晥搸㐳㡥㍡戰㜲摡㔶㠳扢㜴改摡㜵搰㌶㑦昶摥㍤戴㘲搱晤敡戱㌷戶㙦㔲㌲攲㘰ㄱ慥ㅢ㡤ㅣ㜹挸ㄸ昴㑢扣改搱愵㝣㙥㘷㤷㈱㈳て㑦ㄹ〹扢㡣慦㜴ㄹ改捥㉥㘳ㅥㄲ㐸㑢㕣㘸㜰㈴㈲㘸晣㑢㤷搱搰搹㘵挸㐸挴㠳㐶㤳㕤挶户扡㡣㤶捥㉥㐳㐶㈴㥥㌲㌲㜶ㄹ摦改㌲㤶㜶㜶ㄹ㌲㌲昱㤴戱摣㉥㘳戳㉥攳昸捥㉥㐳㐶㈸㥥㌲㔶搸㘵晣愸换攰戰愲㔳㍦戰㌲㔲昱㤴戱捡㉥攳㈷㕤挶㘹㥤㕤挶改㐸攰晤愴慣戶换昸㐵㤷㜱㜶㘷㤷㈱㈳ㄷてㅡ攷摡㘵ㄴㄹ㜲昸攲㜰愳㔳㥢㈲㈳ㄸ㑦ㄹㄷ摢㘵ㄴ敢㌲㉥敦散㌲㘴㈴攳㈹攳㑡扢㡣ㄲ㕤挶搵㥤㕤㠶㡣㘸㍣㘵㜰㘴㈳㐷搱㠰㉥㠳挳㤰㑥㙤㡡㡣㙣㍣㘵摣㘴㤷㔱愶换戸慤戳换㤰ㄱ㡥愷㡣㍢散㌲㠲扡㡣扢㍢扢っㄹ改㜸捡攰㠸㐷㥡搲㕤㤷戱慥戳换㤰ㄱ㡦愷㡣㠷散㌲㝡敡㌲摡㍡扢っㄹ昹㜸捡㔸㙦㤷ㄱ搲㘵㙣攸散㌲㘴〴攴㈹㠳㈳㈱㘹捡搶扡㡣㡤㥤㕤㠶㡣㠴㍣㘵㍣㙢㤷搱㑢㤷昱㘲㘷㤷㈱㈳㈲㑦ㄹ㉦摢㘵㙣愷换㜸扤戳换㤰㤱㤱愷㡣㌷敤㌲㝡敢㌲㌸㥣改搴挳㤷㡣㤰㍣㘵㜰愴㈴晢㐶ㅦ㕤〶㠷㌵㥤㕡㠶㡣㤴㍣㘵㜰挴㈴㘵昴搵㘵㜰㜸搳愹㘵挸㠸挹㔳〶㐷㑥㔲㐶㍦㈹㐳㜱戸㈲㠳戲昷扦搳昷㜶㐶挱愵っ㑦㠲攰〰㐲ㄴ敦攵㈸㜸㑡㉦㡡㜷㜳ㄴ㍣挹ㄶ挵㍢㌹ち㥥昶㡡攲ㅦ㌹ち㥥㠸㡡攲敤ㅣ〵㑦つ㐵昱㔶㡥㠲㈷㙢愲㜸㌳㐷挱搳㈷㔱扣㤱愳攰〹㡤㈸㕥捦㔱昰ㄴ㐳ㄴ慦攵㈸昸愵㉦㡡㔷㜳ㄴ晣ㅡㄶ挵㉢㌹ち㝥㌱㡡攲攵ㅣ〵扦慡㐴昱㔲㡥㠲㕦ㅥ愲㜸㌱㐷挱挳戹㈸㕥挸㔱昰〰㉢㡡攷㜳ㄴ㍣攴㠹攲戹ㅣ〵て㐲愲㜸㌶㐷挱挳㠲㈸㥥挹㔱昰㠳㉡㡡㡤㌹ち㝥㜴㐴昱㜴㡥㠲㍢戳㈸晥㥥愳攰敥㈵㡡愷摣㡡㙥晦ㅦ㈶ㅣ搹㘷 | 㜸〱捤㝤〷㝣ㄴ㘵晡㝦摥㤰㉣㤹愵㘴敤㠸㠸㐱ㄱㄱㄴ㔳㌶挹㉥㠲㤴搰㐵㐰㡡敤搴戰㘵ㄶ㈲㈹㤸㉣〸ㄶ〴㔴㙣㜸搶戳㉢愸攸搹㝢㐵㍤㈳攷㜹ㄶ散㕤㍣摢搹㑥搱㔳捦戳摤愹晦敦昷㜹㘷㌶㌳㍢戳㑢㝥晥㉦㥦㡦㈱晢戰㑦㝦收晢捣捥捥㍢昳扥㤹〲㔵㔰㔰昰ぢ㝥昸㍦㝦㡡昸愶摦慣愵㙤㘹戳㘹㔸㕤㑢㘳愳㤹㐸㌷戴㌴户つㅢ搳摡ㅡ㕢㍡戵愱㉤摤つ〶㠱晡〶攸摢㡡敢摢ㅡ㡥㌵㑢敡ㄷ㥢慤㙤㌰㉡㉥㈸㈸㈹㌱ち愱摦搱㝡㠵㙣挶愰㤷㔱㐴〲慢〲㈳㐰搲㥤愴㠴挴㈰〹㤲昴㈰改㐹搲㡢愴㌷㐹㈹㐹㠸㘴㉢㤲慤㐹戶㈱搹㤶㘴㍢㤲敤㐹㜶㈰改㐳挲晣㐶㕦㤲㥤㐰㝡昶〳㤹㕤㌷㜶㝡晣㈸㙣捤慣㜴㑢慢戹㔷搹㐱扡收㤱ㄵㄵ挳㉡㠶㔵㔶㐵㉢㠶㤵敦㔵㔶户愸㌱扤愸搵ㅣ搹㙣㉥㑡户挶ㅡ昷㉡㥢戱㈸摥搸㤰搸摦㕣㍡扢㘵㠱搹㍣搲㡣㤷㔷挵㘳攱㐸㐵戸扡㍡ㄵ㡤㐶㝡敥㡣挸搳敡挶捥㘸㌵㔳㙤晦慢㤸晤ㄹ㜳㝡摤搸㘱搳捣昴晦㉡收㉥㠸㠹㤰攳㕡㥡㘲つ捤晦愳愰挵散㘹搵㌸㌳搱挰收㥢㘶㙢㐳昳扣㘱㈸摢〵㌴戸摡㘱ㄳ㠰㜸㈲搶㤶慥㌳ㅢㅢ㘷㥡㈹昶扤㘷ㄳ㌱㌳㕢捤收㠴搹搶扢㘹晣㤲㠴搹㘸愹摢㑡㥡づ㡡戵㑥㡢㌵㤹㐵㝣㔳摡愴晢㌶㌹㘹㌶愷ㅢ搲㑢㝢㌵捤㘹㌳㘷挶㥡攷㤹㌴㈹㙥㥡戸愸㈱㔹㔴愴㡡㡡ち扡敤攱㔷㡣昴㘶搸㠴搶㐴摤晣㔸㙢㕡㌸㜶慤挲捦搶戱㠷㐸攱慥戲戸ㄷ㤵㘵㜹戱㑤戳ㅡ㥡昶㌷㕢㥢捤㐶㈶㘱昳㠶㘶ㄹ〹㈶ㅡ晡っ㌸昶搶戰㌱慡㠷昵㜹攳愶㌰㡢㔱㐶㌲〰㈴戰㉢㐸昷㤱㘳㉡㠶搷㤴て㌷㜶愳㜸㈰㠸㉡摡㠴捦慣搳㡤㥦㥢挲晡㔸㘱㝤扣戰㍥㔱㔸㥦㉣慣㌷ぢ敢㔳㠵昵昳ち敢攷ㄷ搶㌷ㄴ搶ㅦ㔵㔸扦〰㌶昶㑦㐹昷敥㠵搶捦㙢攱挷慡慦晡搳愶搱㜷㍣戵昴戹攲敤ㅥ摡㕦昱㘳㉡㥦搷㐱㜸㘳散〱ㄲㄸっ㈲㘵㠴慢㠷ㅢ㝢㔲㍣〴㐴愹㔷㔰〶㑢戹攴㥦㈳㡥㑦ㄵ㑣ㅡ㝤摥愶搸戱改㤵攳扦㔳晣㤴㑢㡣扤㘸扣㌷㐸㘰ㄸ㠸㡥㔱㌹摣搸㠷攲㜲㄰愵㥥戳㘲摣㌱昸㤹ㅢ㡡㥦戹敦㠰昵ㅦ㉦㍥愵攷㤱晤晥愹㜸㤰㤰ㄸ㤵㌴慥〲〹㠴㐱㈴㐶㜵㘴戸㔱㑤㜱つ㠸㔲㑦㕡㌱㜶〸㍥摥敦昵改ㅦ搴慤改晦挹搱昷㍤晤捣㘸挵㝤㑤㘲㐴㘸ㅣ〵〹っ〷搱㌱愲挳㡤㝤㈹ㅥ〱愲搴㥦慤ㄸ摢㉥改昳昵㠷㈷晦㜱摣㠳ㄷ㡦㕣㜴搵搸㕢㍦㔲㍣㐴㐹㡣晤㘸㍣ち㈴㌰ㅡ㐴挷愸ㄹ㙥㡣愱㜸㉣㠸㔲て㕢㌱㝡㙤㌷昱挲摤㘷㝥㜳挰捤㔷㡥扥愱昷㈳愷つ㔶㍣挲㐹㡣㜱㌴ㅥてㄲ㤸〰愲㘳㔴つ㌷㈶㔲㍣〹㐴愹晢慣ㄸ晢扦昸改戲摤㔳㝢㡣㝥攰㥤敤㕥㌸㜴㜴晦扢ㄵて㤰ㄲ㘳ち㡤昷〷〹㑣〵㤱ㄸ㘱挴㌸㠰攲㘹㈰㑡摤㘱挵搸昴晣㥥ぢ㕥㤹㜱攳晥㝦晣攵摢昳ㄲ㔳〶晥㕤㜱㍦㤱ㄸ㌳㘸㝣㈰㐸㘰㈶㠸慥愳㜶戸㌱㡢攲搹㈰㑡摤㘴挵㔸㌵戰敥敢换㡦㍡㜲散昵㝦晢㑦㘰㜲㜹扦愰攲攱㔹㘲ㅣ㐴攳㠳㐱〲㠷㠰攸ㄸ搸㑤て愵昸㌰㄰愵慥戵㘲㡣摤㜰搶慢㍦㕥㝤攵昴攵㉦晣㜱搰愷挱敢敢ㄴ㡦敥ㄲ攳㜰ㅡㅦ〱ㄲ㌸ㄲ㐴㙦ぢ㌰慤愷㜸㉥㠸㔲㙢慣ㄸ㥦摣㍦敥搰愵㉦㡤㥡㜰摤㝥ㅦ挶㐶㝤晡捤㑡挵㉦〷㠹ㄱ愷㜱〲㈴㤰〴㤱ㄸ㔵搸㍦㑣㡡㔳㈰㑡㕤㘲挵戸攳散愳敡㘷㕤昸攵㠴㌵㔳ㅦ㕢㥡㝥慦敥㈴挵敦ㄶ㠹㌱㥦挶つ㈰㠱愳㐰㜴ㅤㄵ挳つ㝥㘶㡣㐶㄰愵捥户㘲昴㕣慦㉥扥㘷敦㙦敡㤶捦ㄹ昷敥昸㝤㕥晢㔲昱慢㐹㘲㌴搳戸〵㈴戰㄰㐴攳ㄱㅥ㙥ㅣ㑤㜱㉢㠸㔲㘷㔹㌱㤶晤昳愹晢晦扥搳挶搱㤷㑦晡攸挶戳㍦㑦摣慥昸捤㈶㌱搲㌴㕥〴ㄲ㔸っ愲敢㐰㡣㘳㈸㕥〲愲搴愹㔶㡣昵㥢攷㔵て㝥攷戲改愷扣㜸攱攰昳㘷扦㜳㠱攲ㄷ愳挴㌸㤶挶挷㠱〴㡥〷搱㌱㠰挷〹ㄴ㉦〳㔱㙡㠵ㄵ攳㤰昳慦㉤㍥㘱捥㔱搳㙦㉡愹晥摡㤸扣㘱て挵敦㔵㠹戱㥣挶㉢㐰〲㉢㐱㜴っ散ㅦ㈷㔱㝣㌲㠸㔲挷㔹㌱〲㉦捣つ愶㝥㜹昰㠰㕢捥ㅤ戶搵搱㉤㕦つ㔲晣㕡㤶ㄸ慢㘸㝣㉡㐸攰㌴㄰㠹㔱㠵ㄸ愷㔳㝣〶㠸㔲㡢慣ㄸ扤㐳㙤ㄷ昵㝥慡㜸攲㌹㜳㡡扦㍢㜸扦㐷〶㈹㝥慢㑢㡣搵㌴㍥ぢ㈴昰㝢㄰㕤〷㍥户㘷㔳㝣づ㠸㔲㉤㔶㡣晢晡搴㍦㍢戲昲㤴戱搷㝣㝣捡ㄷ㝦ㅢ戶昵捦㡡㈷〵ㄲ攳㍣ㅡ㥦てㄲ戸〰㐴搷㠱ㄸ㝦愰昸㐲㄰愵ㅡ慣ㄸ晢㝣戳昲扡㔳慥摥㘹攲㐹ぢ㔷つ昹愴晥扢扤ㄴ捦㈹㈴挶挵㌴扥〴㈴㜰㈹㠸挴愸挶戱昰㌲㡡㉦〷㔱㉡㘱挵搸昵㤷扢て㑣㜵扢㘲摡㕤ㅦ慥㉣扤㘵敤㜶㤷愹㍥㔰㑢㡣㉢㘹扣〶㈴戰ㄶ㐴㙦ぢ㍥㉦㔷㔱㝣㌵㠸㔲㐷㔸㌱㉥㝡晣挳搵搳晥昹昴〱て㍤摦昸㡦ㅥ扢㐴挲㡡㘷㌴ㄲ㘳ㅤ㡤慦〵〹㕣〷愲户〵㥦㤷㍦㔲㝣㍤㠸㔲〷㕢㌱〶晣昰摣搸敦晡㡦ㅣ㜳㘶攲攲昷扦㥡摥晤ㄶ搵ㄷ㙡㠹㜱㈳㡤㙦〲〹摣っ愲户〵晢晡㉤ㄴ摦ち愲搴㠱㔶㡣㌵㥦㍥昶慦㘳挷㕦㌱攵攱㤵捦扣㍤攴攰搳愷㉡㥥㑦㐹㡣摢㘹㝣〷㐸攰㑥㄰ㅤ〳挷昵扢㈸扥ㅢ㐴愹晤慤ㄸ㡢㑦愸㔸戸昳㡦昷散㝦晤摣挵搷㔵摣昹戹敡㜹㉦搴〷㕡㕦㜹攳㕡㘳挷攰扣愱攳㤴愴㜲㔸㌹晦㙤昹㕣っ愷㘲愹敡㔴㙤慡愲㈲㔹㕤ㅥ慢㡡ㄵ㤷㈱㙣㘷捦〰戸㡢昶㑣ㅤ摣搰㥣㙣㌹㐶㑥〹㝡愶㈶㌴㌴愶捤㔶㘱㑡㔳昸㑦㥦搶〸摦㉢㌵㝥〹捥〷ㄳ晡散㘱摢㔴㥤搹㥡挶㜹㔴㝡㘹挷㈹㐵扦戱戱㌶戳㠳ㅤ㙡挵ㅥ摢戲愸㌹搹戶㤳扦㜲㔶㍡㤶㌶晢㘶敢㍡㠲㜸摣㘶攱ㅣ换㙣㤳㤲晡㘷扢ㅤㄴ㙢㕣㘴㡥㔹搲愰搵㍢㘷愹㜱戶搵ㄲ捦慤㥤搰㙡ㅥ㥤搱㝡㉡ㅡ㠳㈱挰㘲㠹敤搹㑡慤搲㜵㤵搵捤㙦㘹㌳㥢愵扣愱㑤㌳ㅡㄲぢ捣搶㔹㈶〷㄰㘶㔲㌶㜵㍢慡慣㔳扥愱搳㥢戱愱㌸㠹㑢敥敡㤴ㄲ㘸戳㌹㘹㈶㔱敦㐲愰扣㜴㜶㉣摥㘸㙥敦㌲搱㌹愱搸搱㈵㥥搰㤲㔸搴㔶搷搲㥣㙥㙤㘹㜴㙢挶㈴ㄷ挷㜰㥡㤹㍣愰㈵㘹ㄶ挹㑦㠱愶慡愰㕢㌷愵ち〶晢㥤慦㌱㜶ㅢ捦攸ㅣ㍢〹捦ㅢ昳ㅢ㍢㜶㈲ㅡ晢㥥〹㘶㈲攳㡤㘳㈷愳晤㥥㜹㉢㜱敥㠴戴㉥捦㙢敤戳㤳搲愹㡦晢㠳㌷㙣㈶晡㠳㍥㌴㥡晣㔴ㄶづ捣ㅤ戲㘳扦摣㐲愵㡥慥㜰扣㐸敢㍣愰㐹搸捣扥搷戵挶㠵㠵摢㔸㕢㍦㝥㌱〶ㄳ㤳㘲捤挹㐶戳㌵敦㘸㔷戱㈲攳㍥㤲晢㐹ㅥ㈰㔹㑦昲㈰㐸昱㌸ㅣ攳㜲㈲㕡〴ぢ戵㐴㉤㉤㍥愶㈱㤹㥥ㅦ㤸㙦㌶捣㥢㥦㠶っ愳攴㤲ㄲ挲敤昹㌱ㅥ㠶挸昸ㄳ挹㈳㈰挱㘰㐱愰ㅤ晦ㄷ〴㠲挶愳昸て㝣昱〰晣晦㝦ㅦ扢ㄴ挲换㤰愱ㄲ挶戲㙤挵㑤ㄸ㤱戵㜵敢收户攵㤳㘲㙤昳搳晣搰攵㔷㌲摥〶㤲㍦㠳昴㝣っ㘴摡㈴戳ㄱㅦ搹晦搵㌰戸㜸㌷挴摣攲㜰㡢愷㍣摢㌷捤㕡摡㥣㤸摦摡搲㡣㡢ㄱ攳㘲改搸㤸〴挶㤴㙤㉡ㄶ㘸㥡摡㔲户㈸ㅤ㘸㥡搴㠰晦㝡㌶捤㌴ㄷ㥡戱㜴ㅤづ挹改㕥㑤㔳㌱ㅥ㤵㘳收攴攴㤲攲㈶㍤㤴ㅣ㘷戶㈵っ㡥㌹㈷攳㄰戴㈴㠰㜷㌸愶昶㙣攲㐱挵㕣㤲㘶攸敥㑤㌳㘲ㄸ戳愶つㄸつㄵ㉦晤㡥㥥扤㐴㘶㝢〷㉤づㄱ㐲昲搶ㄱ愵㠷〸㜴愴〲敥㈵昸戶挴搷㙡㤱㐵戳㍦㉤㜳搲つ㡤㙤挳㉣㜸㠷㡤㙢挱㌵〹㔳㉥挷㄰昶㐰〰㍢㔳㈰㙦戳戲㍦搴ㅣ戴㑥㑦挴㜵㔸㤴㌲戱戵㘵搱挲晥㠸昵扦㡡挳㔸〵挶㕦㐰搶㝣㜵攳扥扢㕦㜱摢㉦搶晦㈷攲攳㈲㍦挶慥戴㘸〷㈱㡢晦攴挷㜸〲晦〵昳改㡡〷挲挲昷愸㥡㘳㝣㕤っ晢㥥㑤搸摡搹慤愶㕣㌰㈸ㄱ㘶改㐲戳㔷搳挱㉤慤ぢ攲㉤㉤ぢ搸晣摥挲戵捤㌷捤㌴㐷攱㍤慣㡢づ㝣慦㤴敡搶捤㌵搶㜶っ搷㜷㐱晣挰㐶㤰㕥㘳ㅡㅢ换散㠸㙤㠱㘷㈰敡㠶㙦㡦挰戳㜸ㄳ慡㈹慦ち搷捥收愹㑤搵戰㈵㡤㙤㑤慡〲㕢捤㜱㜳㑤㜰搱㥦ぢ㜶晥捦㤴昵户ㅤ㕥㍣㍦㜸晡戶慡摣㔲㜸〶攵㠳㄰愷っ㉦攳〵㤲ㄷ㐹㕥㈲㜹㤹攴ㄵ㄰㌵〴慥㍣ㅥ攱扤晢挷㜸つ扣昱㍡挹ㅢ㈰㌸㡡〸昲㌸愸㙣搲慣摡〳晦昳挰㘲扣㐵昲㌷㄰挵㐱㍥㍦㠲〵挶摢㈰㌹晢㌸㤸ㄶ敤㈰㐸㥣挹㙣扣〷㐱搰挸愳㔳㐳㘰挱㕥ㅡ挴捥㈰㕡〶㤱㔲㝤㄰挶ㄷ㤸ㅤ㉣㠵攷㑡挳㕥㜰㉢愳晦愷㈴㥦㤱㙣㈶昹㥣攴ぢ㄰戵ㄵ㕣晤㠱昹㤲㌶㕦㤱㝣つ攲〰收ㅢ捤慡扤昱扦〰昳㙦ㅡ㝤ぢ愲昶〱搱挰㝣㠷㜷㌹㠱ㄹ㐶㠷㜶㄰㈴敦〰收㐷〸㠲㐶ㅥ㥤㉡㠷㠵ㅦ㌰扦晣㥣〳㤸㥦㉤㠵攷昲㐹㈵㈲㤵攱㘵㜴㔳㈰扣戰㙢ㄴ㤳〴㐸扡㠳愸敦攱敡て㡣㐱㥢㈰㐹て㄰〷㌰扤㌴慢慡㄰㜸〰㠳昷愶㔱㈹㠸慡〶慢㠱〹㠱捤〹㑣㤸㕥敤㈰㉥㘰戶㠱㑢搰挸愳㔳㌵㜰昱〳收愳㕣挰㝣㘸㈹㍣搷㠴㈲㠸㔴㠶㤷搱て㐹㡤㥤㐹晡㤳散㐲㔲〶愲摥挹〹捣慥戴搹㡤㘴㈰㠸〳㤸㐱㥡㔵㔱〴ㅥ挰攰㝢搰㘸㌰㠸摡ㄷ慣〶㘶㑦戰㌹㠱ㄹ㑥慦㜶㄰ㄷ㌰㝢挱㈵㘸攴搱愹ㄱ㜰昱〳收㤹㕣挰㙣戴ㄴ㥥ぢ㕤晢㈱㔲ㄹ㕥㐶㌵㤲ㅡ㌵㈴戵㈴ㄱ㤲㈸㠸㝡㍣㈷㌰晢搲㘶〴挹㐸㄰〷㌰愳㌴慢㐶㈱昰〰〶ㅦ㑤愳㌱㈰㙡っ㔸つ捣㔸戰㌹㠱ㄹ㑤慦㜶㄰ㄷ㌰攳攱ㄲ㌴昲攸搴㔸戸昸〱㜳㜷㉥㘰敥戲ㄴ㥥慢㜷攳㄰愹っ㉦㘳ㅡ㤲ㅡ搳㐹㘶㤰ㅣ㐸㌲ㄳ㐴摤㤲ㄳ㤸搹戴㤹㐳㜲㄰㠸〳㤸㐳㌴慢挶㈳昰〰〶㍦㤴㐶㠷㠱㈸㕥つ搴挰晣づ㙣㑥㘰㈶搰慢ㅤ挴〵捣㤱㜰〹ㅡ㜹㜴㙡ㄲ㕣晣㠰戹㉣ㄷ㌰㤷㕡ち捦㈵挹㈹㠸㔴㠶㤷㌱て㐹㡤昹㈴つ㈴㐷㤱㉣〰㔱ㄷ攴〴愶㠹㌶捤㈴㉤㈰づ㘰㡥搶慣摡ㅦ㠱〷㌰㜸㉢㡤摡㐰搴〱㘰㌵㌰㘹戰㌹㠱㤹㑡慦㜶㄰ㄷ㌰挷挰㈵㘸攴搱愹㘹㜰昱〳㘶㘵㉥㘰㔶㔸ち捦㜵搶ㄹ㠸㔴㠶㤷戱ㅣ㐹㡤ㄵ㈴㉢㐹㑥㈲㌹ㄹ㐴ㅤ㤷ㄳ㤸㔵戴㌹㤵攴㌴㄰〷㌰㘷㘸㔶ㅤ㠸挰〳ㄸ晣㑣ㅡ慤〶㔱戳挰㙡㘰捥〲㥢ㄳ㤸㤹昴㙡〷㜱〱㜳づ㕣㠲㐶ㅥ㥤㥡つㄷ㍦㘰ㅡ㜲〱㌳摦㔲慣捡扥㜸㝣㄰㈲㤵攱㘵㕣㠲愴挶愵㈴㤷㤱㕣㑥㜲〵㠸㡡攷〴㘶つ㙤搶㤲㕣〵攲〰收ㅡ捤慡㠳ㄱ㜸〰㠳慦愳搱戵㈰敡㔰戰ㅡ㤸敢挰收〴收㄰㝡戵㠳戸㠰戹〱㉥㐱㈳㡦㑥ㅤ〶ㄷ㍦㘰㘶攴〲㘶扡愵昰㕣ㄱ㍦ㅣ㤱捡昰㌲敥㐴㔲攳㉥㤲扢㐹敥㈱戹ㄷ㐴㑤捥〹捣晤戴㜹㠰㘴㍤㠸〳㤸㠷㌴慢㡥㐰攰〱っ晥㌰㡤晥〴愲敡挱㙡㘰ㅥ〱㥢ㄳ㤸㈳改搵づ攲〲㘶〳㕣㠲㐶ㅥ㥤㥡ぢㄷ㍦㘰㙡㜳〱㔳㘳㈹㍣㤷昹攳㠸㔴㠶㤷昱㌴㤲ㅡㅢ㐹㥥㈱㜹㤶攴㌹㄰㔵㥥ㄳ㤸ㄷ㘸昳㈲挹㑢㈰づ㘰㕥搱慣㑡㈰昰〰〶㝦㤵㐶慦㠱㈸ㄳ慣〶收㜵戰㌹㠱㐹搲慢ㅤ挴〵捣㈶戸〴㡤㍣㍡㤵㠲㡢ㅦ㌰晤㜳〱戳戳愵昰摣扢㤸㡦㐸㘵㜸ㄹㅦ㈰愹昱㈱挹㐷㈴ㅦ㤳㝣〲愲㜶挸〹捣愷戴昹㡣㘴㌳㠸〳㤸㉦㌴慢㜸㉢㘴〰㠳晦㤳㐶㕦㠲愸〵㘰㌵㌰㕦㠱捤〹捣㔱昴㙡〷㜱〱昳つ㕣㠲㐶ㅥ㥤㙡㠴㡢ㅦ㌰挵戹㠰㈹戲ㄴ㥥ㅢ㌲捤㠸㔴㠶㤷昱ㄳ㤲ㅡ㍦㤳晣㐲㔲㔰〸愲㐰搴捦㍦攵㍡昳敤㐶㥢㈲㤲㘲㄰〷㌰摤㌵慢㕡㄰㜸〰㠳㤷搰㠸搳ㅤ搴搱㘰㌵㌰㐱戰㌹㠱㔹㐸慦㜶㄰ㄷ㌰扤ㄸ搷挸愳㔳慤㜰昱〳㘶㌳㌶挲㜷慣昴㤹愵昰摣㘵㑡㈳㔲ㄹ㕥挶昶慣㝤〷㤲㍥㈴㍢㤲昴〵㔱ㅦ收〴愶ㅦ㙤㜶㈶改て攲〰愶㑣戳㙡ㄱ〲ぢ㌰〳㘸戴㉢㠸㍡〶㈲つ捣㙥㘰㜳〲戳㤸㈵戵㠳戸㠰ㄹ挴戸㐶ㅥ㥤㕡〲ㄷ㍦㘰㕥捡〵捣㡢㤶挲㜳敢散㔸㐴㉡挳换搸㠷戵㤷㤳㔴㤰㔴㤲㔴㠱愸㡤㌹㠱愹愶㑤つ㐹㉤㠸〳㤸愸㘶搵㜱〸㉣挰っ愷搱扥㈰敡〴㠸㌴㌰㈳挰收〴收㜸㤶搴づ攲〲㘶ㄴ攳ㅡ㜹㜴㙡ㄹ㕣晣㠰㔹㥦ぢ㤸〷㉣㠵攷㝥攰㜲㐴㉡挳换㤸挴摡㈷㤳㑣㈱搹㥦㘴㉡㠸扡㉢㈷㌰搳㘸㌳㥤㘴〶㠸〳㤸㤹㥡㔵㉢㄰㔸㠰㤹㐵愳搹㈰敡㈴㠸㌴㌰㜳挰收〴㘶㈵㑢㙡〷㜱〱㜳〸㕣㠲㐶ㅥ㥤㍡ㄹ㉥㝥挰㕣㤵ぢ㤸戵㤶挲㜳㤳㜳ㄵ㈲㤵攱㘵挴㤰搴㠸㤳㈴㐸㤲㈴㈶㠸扡㌴㈷㌰昳㘸㌳㥦愴〱挴〱捣〲捤㉡摥㌳ㄵ㘰ㅡ㘹搴〴愲㜸搳㔴〳搳っ㌶㈷㌰愷戱愴㜶㄰ㄷ㌰㐷㌳慥㤱㐷愷捥㠰㡢ㅦ㌰愷攵〲收㔴㑢攱戹㜳扢ㅡ㤱捡昰㌲㡥㘵敤挷㤱ㅣ㑦㜲〲挹㌲㄰戵㈲㈷㌰换㘹戳㠲㘴㈵㠸〳㤸㤳㌵慢捥㐲㘰〱收ㄴㅡ慤〲㔱㘷㐳愴㠱㌹ㄵ㙣㑥㘰㝥捦㤲摡㐱㕣挰㥣挱戸㐶ㅥ㥤㍡〷㉥㝥挰戴攴〲愶搹㔲㜸㙥㐷㥦㠷㐸㘵㜸ㄹ攷戳昶ぢ㐸晥㐰㜲㈱挹㐵㈰㙡㝥㑥㘰㉥愱捤愵㈴㤷㠱㌸㠰戹㐲戳敡㝣〴ㄶ㘰慥愴搱ㅡ㄰昵〷㠸㌴㌰㙢挱收〴收〲㤶搴づ攲〲收ㅡ挶㌵昲攸搴㠵㜰昱〳收愰㕣挰捣戱ㄴ㥥㝢散ㄷ㈳㔲ㄹ㕥挶捤慣晤ㄶ㤲㕢㐹㙥㈳戹ㅤ㐴㑤捦〹捣㥤戴戹㡢攴㙥㄰〷㌰昷㙡㔶㕤㠲挰〲捣㝤㌴扡ㅦ㐴㕤〶㤱〶收〱戰㌹㠱戹㤴㈵戵㠳戸㠰㜹㠸㜱㡤㍣㍡㜵㌹㕣晣㠰ㄹ㤹ぢ㤸ㄱ㤶挲㌳㜱攰㑡㐴㉡挳换昸ぢ㙢㝦㥣攴慦㈴㑦㤰㍣〹愲㙡㜲〲昳㌴㙤㌶㤲㍣〳攲〰收㌹捤慡㌵〸㉣挰㍣㑦愳ㄷ㐰搴㔵㄰㘹㘰㕥〴㥢ㄳ㤸戵㉣愹ㅤ挴〵捣㉢㡣㙢攴搱愹慢攱攲〷捣挰㕣挰散㘶㈹㍣戳㈱搶㈱㔲ㄹ㕥挶摢㐸㙡扣㐳昲㉥挹㝢㈴敦㠳愸㥤㜳〲昳〱㙤㍥㈴昹〸挴〱捣㈷㥡㔵搷㈲戰〰昳てㅡ㝤ち愲㌸扢㐲〳昳ㄹ搸㥣挰㕣挷㤲摡㐱㕣挰㝣挱戸㐶ㅥ㥤扡ㅥ㉥㝥挰昴挸〵㑣搰㔲㜸愶㜸摣㠸㐸㘵㜸ㄹ摦戱昶敦㐹㝥㈰昹㤱攴㍦㈰慡㈸㈷㌰㍦搱收㘷㤲㕦㐰ㅣ挰愸㙥挲慡㥢㄰㔸㠰㈹㠴挰攸〶愲㙥㠱㐸〳㔳〴㌶㈷㌰㌷戳愴㜶㄰ㄷ㌰摤攱ㄲ㌴昲攸搴慤㜰昱〳收敢晦收㌸昳晤捡㔲㜸收慤摣㡥㐸㘵㜸ㄹ㈱㈴㌵戶㈲搹㥡㘴ㅢ㤲㙤㐱搴㘷㜰昵扦ㄸ扥㍤㙤㜶㈰改〳攲〰愶慦㘶搵ㅤ〸㉣挰散㐴愳㝥㈰敡㉥㠸㜶挳ぢ愷捣㘰㜳〲㜳㈷㉤摡㐱㕣挰㤴挱㈵㘸攴搱愹扢攱攲〷捣ㅢ戹㠰㜹摤㔲㘴㑦挶㈹扥て㤱戲㙦㌸捡㠴搵捣㌴〵挷〴㠸摥㌰づ愴收㌴㌷愴摢㝡愴挶㉣㑡户㑣㘸㐸㡦㙢㑢昷㑣㠱攰慤戸昴㤵㍢晡づ愷愱愹㠳ㅡ捣㘳㘶攳㤶摢㉥㕥ㄵ收昲搶㉤㙡㑢户挸扤搴晥㕥晤戸㤶㘹㉤改㜱つ㙤ぢㅢ㘳㑢〷晡愸戵收攰昹㘶㌳愶㤸戴㘲愶挹㤶㡣㕡ㄶ㉥㌴㤳㍥㌵捥㙡㔹搴㥡㌰㈷㡦晢㉤㑣㔲㔱晡愶㜰〱敥㍢㉡㔵愰㜶捦㍤㈹挳㠱晢捥攸㑤㈱敥㔵慡㕦㌹挷愱ㅤ晥㤸搶㡢㕤慦〰㌹戱㥢攳愷愰昸㝥戰昹㜷て挷㤴㤷ㅥ㌰づ愶搰㔲㉤敢㘵捤愹㥡摣摣搶㤰㌴㠳ㄶ㜷㐰㐳㜳㙦敢敤昴㐵㘹㤷㈶戶㘴ㅢ㑢㠳㥢愹搳㥢搱昶㐴慣㌵昹㕢攸〸㌶っ㍦扡ㅤ㉡㠰㝦扦づ㘴ㅤ愶愰攰㑢㕥㡥攰捦㤷㈷ち搰〵挵て㠰昱扤慦㥤昹ㄸ攲㡤㘳戶㔰㈹散㝢ㄱ敡㡣戸㠴摣〱㘶慣㔹㍡㌰㉢㥤ㅣ㘷㉥敥㉤ㄶ㈶㜶㙣㑣㥤㙦㌴户㜱戳㌲扤挱㐸㡤㠹户戵㌴㉥㑡㥢扤㌳敦攴〳㙥愴㘶㥡㡤㌱捥晣敡㤹㜹㌷㈳㤱挶摣戸㑣㍣捥敡晡敤㜴〷㠸ㄴ㔹ㅤ㔲搲愳㐰㥥ㅤ搷扤ㄱ晣散晣捡㡥愲㤱㈹昹昹㘲㤴扡昴ㄲ晥摣㌰慡挰㝥㘳㝤㠸搶㈳㝣攷愷㜶昱㔳戴㡤㍤攳㔰ㅦ搹攴愰搵搳㤶㜱㔶㔵慦㤴ㅣ敦㌰㜵㤲慢㈶㑡昹戱㘹挴㤲㤶㜴㐳㈲搶搸戸戴㜷㙡㜲㜳愲㜱㔱搲㥣ㅡ㡢㥢㡤昶戱扡愵戵改㌷搲慦㈲敥晥扡㔷㜹㜰戱收扢㑤挶㔲㈳㝢㈲搹慦㍥扣ㄵㄸ㐳㜱㘴㤳慦㕡挴搰挷戶〷㔱挴晦㜹づ㕤㄰㑥㕢㜷捣〰㤵㠵㈸㌸愴㜹㐴㍣㤶㜱㡥㔱㘶ㅡ㥥㝣摡ㅣ㘶㔳㕢愶戶㘰㡡㘴搲㈱㥡搴愰㐵扦㤹捦㤴戴㈸㄰〸晣摡㉦ㄵ㘰㠵㥦㉦慤昹て㌸搸㘹㝥ㄴ捦愲昸敤昲㌰昸散搹㐹㡥㤳て昹扥㤷〳㘰〸㠶愵㍣㝡改㤳㠵搹つ改㐶戳㐷㑡昴昲扥㠴ㅦ〷愲搹㍤㌵㝢㍥㘶晡㡣敢㤵㥡搸摡㤰㙣㙣㘸㌶㜹攲㠱㈹扢㕣晣㌳搵㥣㠷挹愵㌳㕡摡ㅡ戸愶慤㔷㙡㜶㙢慣戹㙤㈱㈷㜴㈵㤶㙥敤攲愴㔹挵愹戱つ捤昸昰攸㥣㝣㕦㥡㥡㌵扦攵ㄸ㉣㡢㕢搴搴㍣㌱戶戰敤㌷搱㈸敢慢〴〸改㑦㔴愱㉡㉣㔴㈵㠵㈵扦昶㍢ち㝢㌸㐲㔶㈲㕥㈱㠹搵慡㍦攱㕤㥥捦㉡扢㘴㑤敤攵㘷㤵㌵戹㤶㜸昹捥㌵捣慣㈹攴昱搷搸ㅢㅦ搰㥥挳㐰愶㑣㥣㌳戹㘳㐲昸晦搷〲扤攲㐷㄰㌹捦搷㠰散ㄶ㤹搹愷摢挱戸户摥㔵㈸攳㥥㘳㐸挷挹㘵敦㝥挱㤴搸㜰㑦挴㌷㈷捤昹㜶〲收ち昶挴〷ㅦ㠷㕤捣戱挴昱戶户㘶㜸ち搷ㄴ㙢㙣戳㜴㜵㉤㑤㑤㌱敥㕡摣㉤㘷攱㤸㙤㤶挸昹㌴㡥㈴㐶ち㐴昶㍦㑢ㄴ㕢〲㔱㙣㠹㠸昰㔵捣ㄹ攵昲㥥戱㕡收挵㕡ㅢ搲昳㥢ㅡㄲ㈵㘴㌸敢晢㌷戱㑦㘲ㄷ㉡〲㤸昶㡦散㤸㌸㌹捤㥥捦愹愷㈰愲摤挳㌰㕥㈰㜴㙣㍦昶摣㐲昹晥㔶扦㜲扡㙥㠱㔲㜲愰㌷捡ㄱ慤ㄸ㘳㔹〸慣て㠹攳挴ぢㄲ㌹〸愹㐷㘹㠰㤷㔱〱㜳晢愷㘸〳摥攵㥤㔵搹ㅤ〶挱愹㉤戱攴〴㉣っ㘸㘹敤㙥㉤㈸㉤㐱㙢㜹㐸㘹つ㜱㈶㙤ㅤ愶㥣㘳㉡晢㘲㥣晦戶㤶㔰㌰ぢ㜳㔴㡢㌸〷㌷愰㝢挸て㙤㐱㜱㜱㡦ㄲ扦㕣㤳敤㔸〳慤ㄹ㠷捥〵戹㤳㍤昱㌷ㅦㄸㄹ挵つ〹〶㜹ち㘱㔴㘲㜳㡣㉡㄰昵㘷戰摣㥥㉣㠳㌰つ慡㐱㡡晦〲㘵昶愷㈴攷慣㔳㌸ㄴㄴ㌷㜱㌶㙣㐹ㄳ㌷〷愷ㅡ〱捣㤱挵慣㕡㐰ㄲ攸㔱昲ㄸ昴㐶つ慣㥥搹戸㜱㈴摥ㄷ愸㈷㐰散晣摣㉤慣〲㙢㤹㍦〲愲㕥㠰㤰〳㔱㘹㕢㠱㌱㥣㈹㍡〶㈱敡㐵戰ㅣ㠸搸㍦㡥㉥㕡㍤㝣〹㉡㥥㐲戳㤱㕢㍡ㅤ㔳㉦挳㡥愷㘴戸ㄷ挳ち摡昱捥㍥㈷㔰慦㠰攱㜹㠱晥挹昹捤愵㕥㠳〱扦扤ち㝣㡦㤶敡㜵㘸㜸挴㌴㐶㜲昳摥挰㍢ㅥ㠸㌲㍢收㈸㐸户扣㘳㙥愲〷㕥慥ㅤ㔳扤〵㠹つ愶愳摢㘳戸㈹㘳㤹敤㙦晥〶㜵㌴ㄸ㐷㠳户㘱挰㡥ㅢ攳挱㘵㥡昴㥥挳捤搱愴〹㜴㥢㐸户㑦㘱攰㘸搲㘴挸㥣㑤晡っ㙣晥㈶㙤㠶㐵愷㥢昴㌹㡣㜵㤳愶戰㠲㜶戰㤹㈶㝤〱愶㌳㑤晡ㄲ㜶㜹㥡昴ㄵ搴搲愴愹摣扣慦挱戹㥡㌴つ搲㉤㌷改ㅢ戸㜹㥢昴㙦㐸㝤㥡㌴㠳㥢㜲㈰戳㝤敢㙦㌰㤳〶戳㘸昰ㅤっ愴㐹戳挱㘵㥡昴愳挳捤搱愴㌹㜴㍢㠸㙥摤㔰㡢愳㐹㠷㐰收㙣ㄲ㑦扣昳㌷愹ㄸㄶ㥤㙥㔲〰挶扡㐹㠷戲㠲㜶㈶戳捥慥㔵㜷攸㍡搳㈴㑥㌵捤搳㈴㑥㐲㤵㈶晤㡥㥢搷〳㥣慢㐹㐷㐰扡攵㈶㜱搶㉡㝥戳㍥㐹扤㈱昲㘹㔲㍤㌷㘵㉥戳㤵晡ㅢ挴㘸㄰愷〱㈷扡㑡㤳ㄲ攰㌲㑤攲㕣㔶㍢慥愳㐹㐹扡㤹㜴攳扣㔳㐷㤳收㐱收㙣搲捥㔰攷㙦ㄲ愷慢㜶扡㐹扢挰㔸㌷㘹㍥㉢㜰㌵愹っ扡捥㌴㠹搳㕥昳㌴㘹㌷愸愵㐹㐷㜱昳〶㠲㜳㌵愹ㄱ搲㉤㌷㘹㄰摣昰㥢搵愴㍤㈰戲挱愴搶晡敥㘸收愶戴㌰ㅢ愷搸晡ㄸ㉣愴挱搱㌴攰愴㕢㘹㔲㉢戸㑣㤳㌸慦搶㜶㜳㌴愹㡤㙥晣ㅢㄷ㡡㜳㘰ㅤ㑤㕡っ㤹戳㐹㥣ㅤ㥢扦㐹㥣㍡摢改㈶㜱㡡慤㙥搲㌱慣挰搵㈴捥扣敤㑣㤳㌸〵㌷㑦㤳㌸㌹㔷㥡戴㤴㥢㌷ㄲ㥣慢㐹挷㐱扡攵㈶昱〴〳扦㔹㑤ㅡつ㤱つ㈶戵㔶㤳㑥攰愶㉣㘳戶㌱晥〶㈷搲㘰㌹つ㌸〱㔸㥡戴〲㕣愶㐹攳ㅤ㙥㡥㈶慤愴摢㐹㜴㥢〶〳㐷㤳㑥㠱捣搹愴改㔰攷㙦ㄲ愷昱㜶扡㐹㥣敥慢㥢戴㡡ㄵ戸㥡挴㔹挰㥤㘹搲㙣搸攵㘹ㄲ㈷ち㑢㤳㑥攳收㜱挶戰慢㐹㘷㐰扡攵㈶㜱㘶㌱㝥戳㥡挴改挵㍥㑤㕡捤㑤㌹㡢搹㌸昵搸挷攰昷㌴㌸㥢〶㥣㡣㉣㑤㍡〷㕣愶㐹㥣㙦㙣扢㌹㥡㜴㉥摤捥愳摢㍣ㄸ㌸㥡㜴〱㘴捥㈶㜱搶㜰晥㈶㜱㑡㜱愷㥢挴愹挷扡㐹㝦㘰〵慥㈶㉤㠰慥㌳㑤攲搴攴㍣㑤㙡㠶㕡㥡㜴ㄱ㌷慦〵㥣慢㐹㤷㐰扡攵㈶㜱㤶㌳㝥戳㥡挴愹捥㌶㤸搴㕡㥦愴换戸㈹㤷㌳ㅢ愷㐱晢ㄸ㕣㐱㠳㉢㘹挰戱户㌴㘹つ戸㑣㤳㌸昷搹㜶㜳㌴㘹㉤摤慥愲摢㜲ㄸ㌸㥡㜴つ㘴捥㈶慤㠰㍡㝦㤳㌸扤戹搳㑤攲㌴㘸摤愴㜵慣挰搵愴㤳愱敢㑣㤳㔶挱㉥㑦㤳㑥㠵㕡㥡㜴ㅤ㌷㡦㌳愹㕤㑤扡ㅥ搲㉤㌷㠹㌳慥昱㥢搵愴㌳㈱戲挱愴搶㙡搲㡤摣㤴㥢㤸㡤㔳戲㝤っ㙥愶挱㉤㌴攰㈴㙤㘹搲慤攰㌲㑤攲㍣㙣摢捤搱愴摢攸㜶㍢摤㌸㘷摡搱愴㍢㈱㜳㌶㠹戳愹昳㌷㠹㔳慤㍢摤㈴㑥挹搶㑤扡㡢ㄵ戸㥡㜴〵㜴㥤㘹搲ㅡ搸攵㘹搲㕡愸愵㐹昷㜰昳慥〲攷㙡搲㝤㤰㙥戹㐹㥣晤㡤摦慣㈶慤㠳挸〶㤳㕡慢㐹て㜰㔳搶㌳摢戵晥〶て搲攰㈱ㅡ㕣〷〳㘹搲挳攰㌲㑤攲㥣㜰㍢慥愳㐹㝦愲摢㈳㜴攳晣㙤㐷㤳ㅥ㠵捣搹㈴捥散捥摦愴扢㘱搱改㈶㜱㝡戸㙥搲〶㔶攰㙡ㄲ㘷㡤㜷愶㐹㥣㍥㥥愷㐹㥣㔸㉥㑤㝡㡣㥢挷ㄹ收慥㈶㍤づ改㤶㥢挴㤹攸昸捤㙡搲挳㄰搹㘰㔲㙢㌵改〹㙥捡㤳捣挶愹敡㍥〶㑦搱攰㘹ㅡ㍣〲〳㘹搲㐶㜰㤹㈶㜱㝥扡敤收㘸搲㌳㜴㝢㤶㙥㑦挳挰搱愴攷㈱㜳㌶㠹戳捣昳㌷㠹㔳搰㍢摤愴㘷㘱慣㥢昴〲㉢㜰㌵改㌹攸㍡搳㈴㑥㘵捦搳㈴㑥㜲㤷㈶扤挴捤攳㙣㜷㔷㤳㕥㠱㜴换㑤攲慣㜸晣㘶㌵㠹㔳攳㙤㌰愹戵㥡昴ㅡ㌷攵㜵㘶攳戴㜹ㅦ㠳㌷㘸昰㈶つ㌸㤱㕥㥡戴〹㕣愶㐹㥣㉢㙦扢㌹㥡昴ㄶ摤晥㐶户て㘰攰㘸搲㍢㤰㌹㥢昴㈱搴昹㥢昴ㄱ㉣㍡摤愴㡦㘱慣㥢昴㉥㉢㜰㌵㠹戳改㍢搳㈴㑥慢捦搳愴捦愰㤶㈶扤捦捤攳捣㝢㔷㤳㍥㠰㜴换㑤晡〲㙥昸捤㙡搲㍦㈱戲挱愴搶㙡搲㐷摣㤴㡦㤹㡤㔳昸㝤っ㍥愱挱㍦㘸挰㐹晤搲愴㑦挱㘵㥡昴㡤挳捤搱愴捦攸戶㤹㙥㍦挱挰搱愴㉦㈰㜳㌶㠹戳敦昳㌷改ㄷ㔸㜴扡㐹〵㠵㜶㤳晥挹ち㕣㑤㔲搰㜵愶㐹㥣攲㥦愷㐹㐵㔰㑢㤳扥攲收戱ㅦ慥㈶晤ぢ搲㉤㌷㠹慢〵戰㕤㔹㑤㉡㠱㜴〳愴㔹ㄷ㘲晦捤㑤昹㤶搹っ㝦㠳敦㘸昰㍤つ戸挰㐰㥡昴〳戸㑣㤳㝡㌹摣ㅣ㑤晡㤱㙥晦愱ㅢ攷晢㍢㥡昴ㄳ㘴捥㈶敤〰㜵晥㈶㜱㤹㐰愷㥢戴㈳㡣昵㈷改㘷㔶攰㙡㔲㕦攸㍡搳㈴㉥㌷挸搳㈴㉥㐴㤰㈶㜱慡㡣敡て捥搵愴㐲㐸户摣愴㌲戸㜹㥢㌴〰搲つ摥㈶攱てっ㘲㑤〸戳敤敡㙦㄰愰㐱㜷ㅡ㜰戱㠳㌴愹〴㕣愶㐹㠳ㅣ㙥㤰摢㥦㔰晥㔵㑣㈳㐸㌷慥㍤㜰㌴愹㈷㡤ㅣ㔷挱戹㉡㈱㝦㤳戸㘴愱搳㑤攲搲〶摤愴㕥慣挰搵㈴慥㜸攸㑣㤳戸昴㈱㑦㤳戸㈸㐲㥡㔴捡捤慢〵攷㙡搲㔶㤰㙥戹㐹㔱戸㜹㥢㌴ㅣ搲つ摥㈶㙤挳㑤搹㤶搹戸捣挲挷㘰㍢ㅡ㙣㑦〳㉥扣㤰㈶敤〰㉥搳㈴慥慤戰摤㈰户㥢搴㠷㙥㍢搲㙤ㄲっㅣ㑤摡㠹㐶㡥㈶㑤㠶㍡㝦㤳戸㝣愲搳㑤攲㌲ぢ摤愴㝥慣挰搵㈴慥扥攸㑣㤳戸っ㈳㑦㤳戸㐰㐳㥡搴㥦㥢挷㤵ㅡ慥㈶㤵㐱扡攵㈶㜱㐵㠷户㐹㕣搶戱挱摢愴㕤戹㈹扢㌱ㅢ㤷㝣昸ㄸっ愴挱敥㌴攰㈲㄰㘹搲㈰㜰㤹㈶㜱㥤㠷敤〶戹摤愴㍤攸㌶㤸㙥㌱ㄸ㌸㥡㌴㠴㐶㡥㈶挵愱捥摦㈴㉥攵攸㜴㤳㤲㌰搶㑤ㅡ捡ち㕣㑤㌲愱敢㑣㤳戸㈴㈴㑦㤳收㐳㉤㑤摡㥢㥢搷〰捥搵愴㝤㈰摤㜲㤳戸扡挴摢㈴㉥㌱搹攰㙤㔲〵㌷愵㤲搹戸晣挴挷愰㡡〶㘱ㅡ㜰㐱㡡㌴愹ㅡ㕣愶㐹㕣㜳㘲扢㐱㙥㌷愹㠶㙥戵㜴㍢ㄶ〶㡥㈶㐵㘹攴㘸ㄲ㔷㡥攴㙦ㄲ㤷㤵㜴扡㐹㕣㝥愲㥢㌴㥣ㄵ戸㥡戴っ扡捥㌴㘹㌹散昲㌴㘹〵搴搲愴ㄱ摣扣㤵攰㕣㑤摡て搲㉤㌷改㘴戸㜹㥢㜴ち愴ㅢ扣㑤ㅡ捤㑤ㄹ挳㙣慢晣つ挶搲愰㡥〶㕣ㅣ㈳㑤ㅡ〷㉥搳㈴慥㝦戱攳㐲㙥㌷㘹㍣摤㈶搰㡤㙢㔵ㅣ㑤㥡㐴㈳㐷㤳戸㡡㈵㝦㤳戸挴愵搳㑤攲㔲ㄸ摤愴挹慣挰搵愴㡢愰敢㑣㤳㉥㠱㕤㥥㈶㕤ち戵㌴㘹㝦㙥ㅥ㔷搳戸㥡㜴〰愴㕢㙥ㄲ㔷摤㜸㥢㜴㈵愴ㅢ扣㑤㥡捥㑤㤹挱㙣㕣㤶攳㘳㜰㈰つ㘶搲㘰㉤っ愴㐹戳挰㘵㥡挴戵㌸戶ㅢ攴㜶㤳㘶搳㙤づ摤戸㙥挶搱愴㠳㘹攴㘸ㄲ㔷搴攴㙦ㄲ㤷摢㜴扡㐹㕣㤶愳㥢㜴〸㉢㜰㌵㠹慢㜵㍡搳㈴㉥摢挹搳㈴㉥攸㤱㈶ㅤ挶捤攳捡ㅥ㔷㤳づ㠷㜴换㑤攲ち㈰㙦㤳敥㠳㜴㠳户㐹㐷㜲㔳敡㤹㡤㑢㠴㝣っ收搲㈰㐶㠳〷㘰㈰㑤㡡㠳换㌴㠹敢㠲㙣㌷挸敤㈶㈵攸㤶愴摢㕦㘰攰㘸㔲㡡㐶㡥㈶㍤づ㜵晥㈶㜱改㑦愷㥢昴〴㡣㜵㤳收戱〲㔷㤳㥥㠴慥㌳㑤攲ㄲ愲㍣㑤攲攲㈲㘹㔲〳㌷㡦慢㡣㕣㑤㕡〰改㤶㥢挴搵㐸摥㈶㜱㐹搲〶㙦㤳㥡戸㈹捤捣挶攵㑡㍥〶㉤㌴㔸㐸〳㉥㘰㤲㈶ㅤつ㉥搳㈴慥㔱戲摤㈰户㥢搴㑡户㌶扡扤つ〳㐷㤳ㄶ搱挸搱㈴慥㌴捡摦愴㜷㘱搱改㈶扤〷㘳摤愴挵慣挰搵愴昷愱敢㑣㤳戸㥣㈹㑦㤳㍥㠴㕡㥡戴㠴㥢昷ㄱ㌸㔷㤳㡥㠵㜴换㑤晡〴㙥摥㈶晤〳搲つ摥㈶ㅤ捦㑤㌹㠱搹戸㜴捡挷㘰ㄹつ㑥愴〱ㄷ㔳㐹㤳㤶㠳换㌴㠹敢愵㙣㌷挸敤㈶慤愰摢㑡扡㝤〷〳㐷㤳㑥愶㤱愳㐹㕣昵㤴扦㐹㍦挰愲搳㑤晡ㄱ挶扡㐹愷戰〲㔷㤳戸愲慡㌳㑤攲搲慡㍣㑤晡ㄹ㙡㘹搲愹摣㍣慥扥㜲㌵改㜴㐸户摣㈴挵㜱㍥㤰㜰捦ㄶ㉡㠴㜴〳愴㔹㔷ㅣ捥攴愶慣㘶戶㙥晥〶㘷搱攰昷㌴㈸㠲㠱㌴改㙣㜰㤹㈶㜵㜷戸㐱㙥㌷改ㅣ扡㥤㑢户㄰っㅣ㑤㍡㥦㐶㡥㈶㙤〵㜵晥㈶㙤つ㡢㑥㌷㘹ㅢㄸ敢㈶㕤挰ち摡㤹捣㥥㠸戲㉤㜴㥤㘹搲昶戰换搳愴ㅤ愰㤶㈶㕤挸捤敢〳捥搵愴㡢㈱摤㜲㤳晡挲捤摢愴㥤㈰昵㘹搲愵摣㤴换㤸㡤㑢捡㝣っ㉥愷挱ㄵ㌴搸ㄹ〶搲愴㉢挱㘵㥡㔴收㜰㠳摣㙥搲ㅡ扡慤〵㈹ㅥ〲㠳捥慤㉥攲㙣挷㤰㘳挹ㄷ攷挶戶㙤㤵㍡㜰㔱慣ㄱ捦㘴㤸㡥昵〷㘹㡡㝥ぢ㤳㑦㡢昴㉡㤰散㍦〵敤㝥㔴〳ㄶ㑥挹㈶晣敥㠸晥搸戲㙣っ摣戶搶戶戵搱昲搷慤ㄲ〹ㄶ搷晦攷㤷㕦㍡㤷㠵扢㐷昷挵晣换愳昵昵〵㈵捣㠹㈶㘱㌹攰搵㘸ㄸ攷捣㜳ㅤ㐳㥥㠹搸㔹㡢㈶ㄸ㙤㥢㡥㘹愳㥣㈰㍣戴㤱㑦㜱昱㥢㙦敡㥥㡦㝤つㄲ㉡㑥捡㤶ㅤ㜶ㅤ㌹〴攳慢戸ㅣ搲㉤捥攵㠵〳㔶㠳㜱㔶敦慣昴搲㐶捣愴收㕢晥慤㑤晤㡥㔳㐷戵ㅡ攵戵戴ㄶ㘱搱㕢昶㕦搲捤昸摥㡢㔰㍤戶捤晡换挵攲㐶捤㌰㔴㔳晣㍢〰㥣搳㥦㐵㜷㘰㑡ㅦ晥〴慥㐳㠹摢ㅥ搰㤰㘸㙤㘹㙢㐹愵换㘶㘱㌵㐰ㄹ晦㤶㌵晥㐴㑦昹㤸攲㐳ㄱ搱㌷㈷㌷慣愸㤹てㅦ㤱㌶〵ㄷ㌴户ㅣ搳㉣搵ㄴ户昱㑦㝡ぢ㕥摤扢㌳つ㔷㡢挸捦㙥〰㉥㔴㠱㐲昹ㄳ慡戴㔰つ㕣㡦㔸扢搷㡤慤㥢㔹ㅦ㑥㈵慢㈲攵攱㥡昲㐸戴㈶ㅣ㡥㈷㘲㔵㤱㜸㜹㍣㥡㡡搶㥡搵搱㐴慤ㄹ慡戲㝣㡣ㅢ攰ㄳち摢摣㡤攴慡㙤㡥扡搲ㅡ㜰㑣ㅣ㤰㘴晦㐳ㄲ慡㐵㘴晣攲敦挶㈳捦㔶㜵㘳敢摤㡦㘶〹摣〲㜱㑦㠸㘵㙥昳㑣晣〱敤挰慤㤰昴㠶挴戱㍥㈰ㄴ戱愲ㄸ户㐱㘹っ㐰㍣愳っ㐴つ㠷㥣㐷愴愰㥡〶攸昹㠹㘱慥愰㜱ㄷ捣戰攷慢㝤挱㜲敦㌷敥㠶㐰㡤挴㍢㐱晡ㅥ㜲昴攷㙢ㄴ愴摣㍢搵ㄴ戸㜳㥦㠰戰挰㘰愳搹㔳㌵〹ㄲ昶搵摤㤷㌱㔶愸挰〳戰搳敤㠸㠵㙢慢㉡㉢㔳搱㜰戵㤹〸㐷㙡攲㔱戳摡慣㑡㤵㠷愳ㄵㄵ攱㘴㌸ㄵつ㡤戵搳慦㠷㑦愸捥收愴ㅤ攳㙣㡥扡㔲捥戲敤㥡㜶㑣㐰㘴晣ㄶㄸ㙣㠷㐱昰つ攲ㅤ攲㜴㕤㤱户㔳戴〷㉤〶㠱㈸㑥搹搵〰㡦〴〶ㅤ〰㍦〶㌳〲㍣〵㝡〱昸㉦㄰愸愹攰〴攰挷挹搱㥦慦㘹㤰ち挰㔱㠴昰〲㕣敢ぢ昰っ㉢㔴攰㈹㠴搲〰挷㙢㔲㤱㘴㐵㔵㜹㌲㔱㕢ㄵ㑥愴攲㤱慡㑡戳戶扣㍡㤹㡡㔵搵㔴㔴㔶㔵㠶づ戴搳㍦つ㥦搰㑣㥢ㄳ㠰㘷搹ㅣ㜵愵戳挱㜵つ挰㜳㄰ㄹ扦ㅥ㠰て戲攵㉦㈰扦㍣摤挶搸㡢攰ㅣ〲戹〶㜸㉦ㄷ挰慦挰㡣〰ㅦち扤〰晣㉡〴敡㜷攰〴攰搷挸搹〰ㅦ〱愹〰㍣搸ㄷ攰㐱扥〰搷㕢愱〲㥢㄰㑡〳㥣㡣㠶攳㤵戵㠹㜰㉡㔱㤱ち㐷挲戵昱敡昲㐴㈲ㄹづ㤷㈷㉢㉢攳攱㥡敡搰㕣㍢晤㕢昰〹挵㙣㑥〰㡥摢ㅣ㜵愵〹㜰㕤〳㜰ㄲ㤱昱敢〱㤸搳㘴㐵晥㍥昲换愳㝦っ慥㐵㔲㥣㉡慢〱摥挹〵昰㐷㌰㈳挰昳愱ㄷ㠰㍦㠶㐰ㅤ〵㑥〰晥㠴㥣つ㜰㈳愴〲昰づ扥〰㙦攷ぢ㜰戳ㄵ㉡戰ㄹ愱㌴挰攵愹㔴㌲㘶挶㔳ㄵ挰㌵㕣㔹ㄱ㡢搵搶搶愶愲挹㐸㘵㍣㥥㐸㔵㐷捤㤰㑣㑦攵挶㝤づ㥦搰㐲扢ㄸ〱昸㘸㥢愳慥戴ㄵ㕣搷〰摣㠶挸昸昵〰㥣戶攵晦㐲㝥㜹㉥㤲ㄱ㈱㐰㡢㈱搷〰〷㕤〰㝦〷㌳〲㝣っ昴〲昰昷㄰愸愵攰〴攰ㅦ挸搹〰ㅦ〷愹〰ㅣ昰〵戸挸ㄷ攰ㄳ慣㔰㠱㥦㄰捡㍡〶㔷㐵㙡慡㉡㈳㠹㔴戹㠹㐳慥㔹ㄳ挵户愲㔹ㅢ慤㠸㥡戵戱㘴慡扡㍣㈴㔳㑢戹㜱㍦挳㈷㜴愲㕤㡣〰扣摣收愸㉢㕤〱慥㙢〰㕥㠹挸昸昵〰㝣㤲㉤㉦㉡㠶㜲ㄴ㉤昶㈳㐰㥣愲慡〱晥攱㐷攷㌱戸〴㘶〴㜸ㄵ昴〲㌰ㅦ㤴愷㑥〳㈷〰〷挹搱㥦慦㌳㈰ㄵ㠰晦㡤㄰摥㘳昰扦㈰昵㝥挹慤戶㐲〵㝡㈳㤴〶戸ㄶ㝢慢ㄹ慤慥㡡㔵㠶㘳攱㔸㌹ㅥ㠲㔷㔹ㄹ㈹㑦㈴㙢㤲㠹㐸戸㍡ㅥて挹戴㔰㤶㕥ち㥦搰敦敤㘲〴㘰㤹ㄱ㙡敢㑡捦㠱慥㙢〰㍥ㄷ㤱昱敢〱昸㍣㕢扥ㅤ㙡㤳㈷㙡ㄹ攳〸捥〵㤰㙢㠰㍦㜱〱扣㈳捣〸昰ㅦ愰ㄷ㠰晢㐲愰㉥〲㈷〰敦㐴㡥晥㝣㕤〲愹〰晣㠱㉦挰敦晢〲㝣㤹ㄵ㉡戰ぢ㐲㘹㠰挳戵㤵㌵㌵搵ㄵ搸㙢换㈳攱捡敡㘸㍣㕥ㄳ㡦㈷㔳㌵戱㐴㘵っ晦㐷㐲㌲愵㤳ㅢ㔷〶㥦搰ㄵ㜶㌱〲戰捣收戴㜵愵㙢愰敢ㅡ㠰搷㈲㌲㝥㍤〰㕦㘵换〷愱㌶㜹摣㤸㌱㠵攰㕣〳戹〶昸㌵ㄷ挰㐳㘰㐶㠰搷㐱㉦〰て㠵㐰㕤〷㑥〰摥㡢ㅣ晤昹扡ㅥ㔲〱昸㈵㕦㠰㕦昰〵昸㐶㉢㔴愰ㅣ愱㌴挰㔵搵昸㡡㡢㤵㠷㑤ㄳ㝢㉣㡥ㄳ㌸㍤慢㠹㥢攱㘴㜹㘵㍣㔹㔳㕢㤱っ摤㘴愷慦㠰㑦攸㘶㥢ㄳ㠰㘵㈶㈶㌷㥣扡搲㕢愱敢ㅡ㠰㌹㝦ㄳ扦ㅥ㠰㙦户攵戵挸㉦捦㘲㌳㘶㄰㥣㍢㈱搷〰㍦敥〲㜸㕦㤸ㄱ攰扢愰ㄷ㠰㐷㐰愰敥〱㈷〰㡦㈴㐷㝦扥敥㠳㔴〰摥攰ぢ㜰扢㉦挰て㔸愱〲㘳㄰㑡〳㡣㌳㌴ㅣㅣ慡㉢㤳㤱昲敡㜰㉣ㄶ㡢㤸㌸㌱慥㠹㥡戱慡慡㐸㔵㡤ㄹて慤户搳㡦㠵㑦攸㐱㥢ㄳ㠰㘵ㄶ㈵㌷㥣扡搲㠷愱敢ㅡ㠰㌹昷ㄲ扦ㅥ㠰ㅦ戱攵㤳㤰㕦ㅥ㔴㘷ㅣ㐴㜰ㅥ㠵㕣〳㝣㡦ぢ攰愹㌰㈳挰ㅢ愰ㄷ㠰て㠰㐰㍤〶㑥〰㥥㐶㡥晥㝣㍤づ愹〰㝣㠷㉦挰户昹〲晣㠴ㄵ㉡㌰ㄳ愱㌴挰戱㥡愴㔹ㄵ㡥㈶㘳ㄵ攵戱㜰戲慡㉡㥥㡣搵㠴㈳搱㘸㙤㉣㔲㔵㤱〸㔷㠵㘴ㅡ㈴㌷㙥ㄶ㝣㐲㑦搹挵〸挰㑦摢ㅣ㜵愵ㅢ挱㜵つ挰㥣㌷㠹㕦て挰捦摡昲㐳㤱㕦㥥攲㘷ㅣ㑥㜰㥥㠷㕣〳扣捥〵昰ㄱ㌰㈳挰㉦㐰㉦〰ㅦ〹㠱㝡〹㥣〰㕣㑦㡥晥㝣扤〲愹〰扣搶ㄷ攰㉢㝤〱㝥捤ちㄵ㐸㈰㤴〶㌸ㄲ㐹攱㠹慤ㅣ㔵㐴慢挲ㄱづ慦慢㤳㌸㘳㑢㈵捤㜰戸戲戶摣っ扤㙥愷㑦挲㈷昴㠶捤〹挰㙦摡ㅣ㜵愵㥢挰㜵つ挰㥣昳㠸㕦て挰㝦戳攵㐷㈱扦㤱愰㐵㥣攰扣〳戹〶昸㝣ㄷ挰㝣〶㉦〱㝥ㄷ㝡〱戸〵〲昵㍥㌸〱㜸㈱㌹晡昳昵〱愴〲昰搹扥〰㥦攵ぢ昰㐷㔶愸㐰ㅡ愱㌴挰㐹っ㌲㙡㙡㌰扣㐸㔶挶挲ㄵ愹敡㐸㈲㠶㠱㜲㑤㈲㔵㔹ㅥ㡤攰㑣㉤㈴搳て㔹晡㈲昸㠴㍥戱㡢ㄱ㠰㘵收愱慤㉢晤ㄴ扡慥〱昸㌳㐴挶慦〷攰捤戶晣㌸搴㈶捦㝦㌴收ㄳ㥣㉦㈰搷〰慦㜴〱㝣㈲捣〸㌰㘷ㅦち挰换㈱㔰㕦㠱ㄳ㠰㔷㤰愳㍦㕦晦㠲㔴〰㕥收ぢ昰昱扥〰晦摢ちㄵ㌸〵愱㌴挰ㄸ㘲挴㈳挹㥡㡡㔸㌲㤲〸挷愲搵戱㐸㙤㈴㤲愸愹㌱㈳㌸扤愸づ挷㐳摦摡改㔷挱㈷昴㥤捤〹挰摦摢ㅣ㜵愵㍦㠰敢ㅡ㠰㝦㐴㘴晣㝡〰晥㡦㉤㕦㡤晣昲㜰㑣愳㤹攰晣〴戹〶昸㘸ㄷ挰攷挰㡣〰㜳收愰〰㝣㉥〴昲〷戱〴攰昳㠴戳〰㉥挴愹扤〰摣攴ぢ昰〲㕦㠰㡢攰挴㔰㠱ぢㄱ㑡〳㕣ㄳ㡤㥡㔵㠹摡㡡㥡㐴㙤㌲ㅣ慤慥㡤㔷㔵攱搸㡢挷ぢ㤶攳ㅡ㐵戲㈶ㅡ㉡戶㝣㡣㡢攰ㄳち搸㥣〰摣摤收愸㉢㉤〱搷㌵〰ㅢ㠸散〷㜰搰㤶㕦㠱晣昲攴㔰㈳㑤㠰㝢㐲慥〱㥥敢〲昸㉡㤸ㄱ攰㕥搰ぢ挰㔷㐳愰㑡挱〹挰搷㤰愳㍦㕦㕢㐱㉡〰ㅦ敥ぢ昰㘱扥〰㙦㘳㠵ち晣ㄱ愱㌴挰㤵搱㐸㉡㕡㠳昱㜲慡愶㌶ㅣ慦愹㡡㔴㠷㙢慢慢昹挵㔷㘵㈶攲攱摡搰戶㜶晡敢攱ㄳ摡捥收〴攰敤㙤㡥扡搲ㅤ挰㜵つ挰㝤㄰搹て㘰㑥晢ㄳ昹慤挸㉦㡦㔵㌵㡥㈵㌸㥣晡愷〱㥥敥〲昸㑥㤸ㄱ攰㝥搰ぢ挰㜷㐱愰晡㠳ㄳ㠰敦㈶㘷〳㕣〶愹〰扣扦㉦挰㤳㝤〱摥搵ちㄵ戸ㅦ愱㌴挰搱㡡昲慡昲㔴㑤愵ㄹ挷㌹〳㑥捣攲愶ㄹ慥㉡慦慤㌵挳愹㙡㥣ㅣ挷㐳㌲摤づ㔹㡤〷攰ㄳㅡ㘸ㄷ㈳〰敦㙥㜳搴㤵づ〲搷㌵〰敦㠱挸㝥〰て戶攵㡦㈰扦戱㠲㔵㉥㈷㐰㐳㈰搷〰敦攷〲昸捦㌰㈳挰㐳愱ㄷ㠰ㅦ㠳㐰敤つ㑥〰晥ぢ㌹晡昳戵て愴〲昰㜰㕦㠰㈳扥〰㔷㔸愱〲㑦㈲㤴〵㜰㍣㙥搶㐴攲㤵搵搵戱㈸㉥昶愴攲挹㐸㍣㔱㔱㘱搶㈶ㄳㄸ㉣㈷㔳㈱㤹㉡㠷㡣挶㔳昰〹㔵搹挵〸挰㘱㥢愳慥戴ㅡ㕣搷〰㕣㠳挸㝥〰搷摡昲攷㤱㕦ㅥ挸㙢慣㈲㌸㥣㜲愷〱摥摢〵昰换㌰㈳挰挳愱ㄷ㠰㕦㠱㐰㡤〰㈷〰扦㑡捥〶㜸㍦㐸〵攰㍤㝤〱摥挳ㄷ攰搱㔶愸挰㥢〸愵〱㑥㈴慢㘳㤵戱㐴㌹㉥扡㈷挳㤱戸ㄹ㡦㔷㐵㤲戵搱㘸㌴ㄹ慦慣㠹㐵㙢㐳㌲捤㡤〰㙦㠲㑦㘸慣㕤㡣〰㉣㌳摣㙣㕤改㌸攸扡〶攰昱㠸散〷昰〴㕢晥ㅥ㙡㤳愷ㄵㅢ慢〹搰㈴挸㌵挰晤㕣〰㝦〸㌳〲㍣ㄹ㝡〱昸㈳〸搴晥攰〴攰㡦挹搹〰ㅦ〰愹〰摣挷ㄷ攰敤㝤〱㥥㙥㠵ち㝣㠶㔰ㅡ攰摡㘸㉣㔵㠱㡢㍣戸㥣㔶ㄵ慥づ〳搸慡㈴㡦ㄲ戸ㄸㅣ挶ㄵ换昲㤰㑣㔱㈳㠸㥢攱ㄳ㍡搰㉥㐶〰㤶搹㘹戶慥㜴ㄶ㜴㕤〳昰㙣㐴昶〳㜸㡥㉤晦ㅡ戵挹愳㥣㡤昳〸搰挱㤰㙢㠰㝢戸〰晥ㄶ㘶〴昸㄰攸〵攰敦㈰㔰㠷㠱ㄳ㠰扦㈷㘷〳㝣㌸愴〲㜰㜷㕦㠰㡢㝤〱㍥搲ちㄵ昸㉦㐲㘹㠰㔳ㄵ㔵㔵搵㤱㔸㑤㐵㐵㍣ㅡ慥㑤㈶㘳愹㘸㌴㥥㡡㐶捡愳戸㔲ㅣ㡥㔵㠵㘴㝡ㄹ㐱晣〹㍥愱戹㜶㌱〲戰捣㉣戳㜵愵㜱攸扡〶㘰捥㐷昳〳㌸㘹换扢攱慥愱㍣攷摡戸㤸〰愵㈰搷〰晦昸㠳昳㜲㘵㜷㤸ㄱ攰㜹搰ぢ挰㈵㄰愸〶㜰〲戰㐱捥〶㜸〱愴〲昰户〸攱扤㕣昹つ愴摥换㤵㑤㔶愸㐰㉦㠴搲〰挷攲㌵㌵攱摡昲㔸㌴ㅡ㑢㠶㙢㉡㙡愳昱㙡㍣晤㌹㔶ㅤ慦愹挴㔰愳愶㌶㈴㔳挳〸㘲㙦昸㠴㕡散㘲〴㘰㤹ㄵ㘶敢㑡㡦㠶慥㙢〰收㕣㌲㍦㠰摢㙣昹戶愸㑤ㅥ〲㙥㕣㐹㠰ㄶ㐱慥〱晥㠷ぢ攰㍥㌰㈳挰㡢愱ㄷ㠰㜷㠴㐰㉤〱㈷〰昷㈵㘷〳㝣㉣愴〲昰㠷扥〰晦摤ㄷ攰攳慤㔰㠱晥〸㘵〳㕣㘵㥡㤱昲㡡ㄸ㡦挱㈶㐶㜲㤱㜸㌴㘱攲㍢て㤷㌰㉢㔲愹摡㤰㑣敢㈲㠸扢挰㈷戴捣㉥㐶〰㤶ㄹ㕤戶慥㜴㌹㜴㕤〳㌰攷㠱昹〱扣搲㤶敦㡥摡㡣㙢㔹挹㍡〲㜴㌲攴ㅡ攰搷㕤〰敦〹㌳〲㝣ち昴〲昰㄰〸搴愹攰〴攰愱攴攸捦搷改㤰ち挰㉦晢〲晣愲㉦挰㘷㕡愱〲晢㈰㤴〶搸慣挲敤捥昲㐸㑤慤㔹㥥ち㈷㘲㌵戸愰㘶㐶捣ㄸづ挷㌸ぢ挶改㕢㘸戵㥤扥ㅣ㍥愱戳㙣㑥〰㤶搹㔸摣㉣敡㑡捦㠶慥㙢〰收ㅣ㉥㍦㠰捦戵攵㌵挸㉦㡦㡦㌷㙥㈴㌸攷㐳慥〱晥慢ぢ攰攱㌰㈳挰ㄷ㐰㉦〰敦ぢ㠱扡㄰㥣〰㍣㠲㥣つ昰挵㤰ち挰㝦昶〵昸㔱㕦㠰㉦戵㐲〵㐶㈳㤴〶ㄸ㌷㤰㘳搱昲㈴慥愲㤵攳敡㑥㈴ㄲ慤挶㤷㕤㌴㙣搶㐶㉡㉢㈲㔵愹慡㤰㑣愷㈲㠸㘳攰ㄳ扡摣㉥㐶〰㤶㤹㔴戶慥昴㑡攸扡〶㘰捥扦昲〳㜸慤㉤㥦㠸摡っ晥㔱㜱㠳㝦戶㕣㕤㙤㔷㌹〵㜲㍡昲愵㘴㝡づ㙤㉡挸㕡㍦愱㜵戰挵㉦㥥捤〲摢㕥摤㡡㙦〰攳晢㌷㑥昵捣㡤㔹昸换㜵收戰扡戱戵挳挶㉦㐹㤸㡤晣㕢戲㤸戶〱搷㠲敤㥡㈶户攱㉤ㅥ攸㍣扢㘵㡣晣㤵㔳㑥摤搹捡㥥搹㌱搴㝥㤸昴敥ㅤㄲ晢て〹摢㙥搳㕢㌳㝥㜸㌶㌲㈶㌴㐱㌱㤴㡦㥥摥慥㠳㜳㍣ㄵ㜹愷づ㈹晥㘲㌴晥㤶慤㤹戴㈳戶㘱㌶㕦㔱㘱㌷㌵挴敦㉦㘱㕢㑦晥挵挳㜶敤〰攳㥢ㄷ㌵敤㠲㙤搸挹攷捦收㡤㙤㐸换㌴愷㝥搰㉢攳㝡挰ㄳ㤸㠶敤㉤ㅥ㌹㜰攲挰㐸昱ㅤ搸搱晥て㐹戸晦㜶捣㉢㘲㑡晥〴㡤ㄹ㠸愸戸㑦㌱ㅥ㐵敡㌶㌰〳昱㈶晢㜹户㌷挳㘰ㄳ晥昸扢攷㐱挰㌷㔹ち捦㠳㠰敦㐲㈴昹〰ㅤ㠴㈴㤹扤攱㙥㕢敡摡ㅢ敥㠱ㄴ扦〵挶㈱戰敤搵㑤慤〷挳㍤㐲ㄹ㥣改ㄲ㌸㑣㙦昸㠴㠱㌵敡㕡愴戳㡢つㅡ㠷戳晥㜶㤸っ昴㈹㜹㙤慥㤲搷㔸ち捦㈳㝡ㅦ㘳㑡㐶㡡㍢㑢晥㡢㉤㜵㤵晣㌸愴昸挵愴㜹㕤昲搳㘰㜴挹㑦攱㕤㠰晢㈶㝡㔵㠷㤲㉦㜱㤵㍣㥦㈵扦〰㤳㠱㍥㈵㕦㤰慢攴昳㉤㠵攷攱戹慦㈰㤲㤴摣散㉣昹㔵㕢敡㉡昹㌵㐸昱㡢㤹攷扡攴户挰攸㤲㌹ㅢ㈳搰慡㑢ㅥ㍦㌰愲捥㜲㤵㥣㘶挹敦挳㘴愰㑦挹愷攵㉡昹㔴㑢攱㜹慣敤㐷㠸㈴㈵ㅦ敢㉣昹㘳㕢敡㉡昹ㄳ㐸昱㡢㐷昳攸㤲㍦〷愳㑢收晣㠶挰㌲㕤昲〴㤴扣挲㔵昲㜲㤶晣㉦㤸っ昴㈹昹昸㕣㈵ㅦ㘷㈹㍣て㥣晤づ㤱愴攴㔵捥㤲扦户愵慥㤲㌹挵〰扦㜸㈸愶㉥昹㘷㌰扡㘴捥ㄸ〸㥣愱㑢慥㐳挹㡢㕣㈵慦㘶挹扣〹㍦搰愷攴㠵戹㑡㙥戱ㄴ㥥㐷挱昲㍥扤㤴㝣㥥戳㘴戹㔹捦昸慥㤲㠳戰㤵㤲㉦搰㈵昳㉥扡㉥㤹昷攰〳ㄷ敡㤲㈷づ慣㔵つ慥㤲㉦㘶挹扣慤敤㔷㜲㌲㔷挹〹㑢攱㜹㐸㉢敦㝣㑢挹㔷㍡㑢㤶摢摦㥥㤲㜹ㅢ㕣㑡㕥慢㑢收㝤㘹㕤㌲敦㙡〷慥搶㈵㡦挳挷敦〸㔷挹敢㔸㌲㙦ㄴ晢㤵㝣㐸慥㤲て戶ㄴ㥥挷愷づ㐱㈴㈹昹㐶㘷挹㜲㐳搹㔳昲㕥戰㤵㤲㙦搶㈵昳㙥慥㉥㤹昷㠹〳户摡㈵㐷搴㠱慥㤲㙦㘷挹扣昵敡㔷昲搴㕣㈵敦㙦㈹㔶㘵㍦搸㤴㜷㘷愵攴㝢㥤㈵换㉤㕡㑦挹扣㔵㉢㈵摦慦㑢收晤㔱㕤㌲敦扣〶搶摢㈵搷慡昱慥㤲ㅦ㘲挹扣㤹改㔷昲攸㕣㈵㡦戲ㄴ㥥㐷㡥㑥㐵㈴㈹㜹㠳戳㘴戹改改㈹㤹㌷㍦愵攴挷㜴挹扣攳愸㑢收扤捣挰攳扡攴㠹搸㌱愲慥㤲㥦㘰挹扣㍤攸㔷㜲㌸㔷挹㔵㤶挲昳㌰㔰摥㐱㤴㤲㥦㜵㤶㉣户ㄱ㍤㈵昳㜶愲㤴晣扣㉥㤹昷昰㜴挹扣㍢ㄸ㜸㔱㤷㍣㘱㘰戵摡摢㔵昲换㉣昹㈸㤸昸㤵㍣㌸㔷挹㝢㔸ち捦㘳㍡㜹㑦㑥㑡㝥搳㔹戲摣㤸昳㤴捣ㅢ㜴㔲昲㕢扡㘴摥㌱搳㈵昳㝥㕢攰㙤㕤昲㔸愰㍣挰㔵昲扢㉣㤹户戰晣㑡敥㤷慢攴㥤㉣㠵攷〱㥡扣换㈵㈵㝦攴㉣㔹㙥㜵㜹㑡收㉤㉦㈹昹ㄳ㕤㌲敦㌳改㤲㜹〷㉢昰愹㉥㜹っ㡥换摢戹㑡摥捣㤲㔷挳挴慦攴㔰慥㤲㑢㉤㠵攷搱㤶扣㙦㈴㈵㝦敤㉣㔹摦㍣捡㍥㉥昳㈶㤲㤴晣㡤㉥㤹㜷㙥㜴挹扣㈷ㄴ昸㔶㤷㍣ㅥ㈸ㅢ慥㤲扦㘷挹扣捤攲㔷㜲㔱慥㤲扢㔹ち捦㐳㈷㜹㈷㐶㑡晥搹㔹戲摣㡥昱愰捣摢㌲㔲㜲〱㔶㘲攰㑣㡥昷㐲㜴挹扣换ㄲ㈸㠴ㄴ愷㐵㘳昱㔵昲搳昷捥㌳戹㈲㈸ㄴ㙦㕣昸㤵晣㍤㑣㝤㑦㍥扦戳ㄴ㥥挷㐱昲摥㠶㤴ㅣ㐴摣捣挹愷摣攰昰㤴捣ㅢㅤ㔲㜲㑦㕤㌲敦㉥攸㤲㜹摦㈲搰㕢㤷㍣〶㈵㝦攵㉡㌹挴㤲㜹㉢挰慦攴捤戹㑡晥捣㔲㜸ㅥ搴挸扢〵㔲昲昶捥㤲攵㤶㠱愷㘴摥㍡㤰㤲晢攸㤲㜹扤㕥㤷捣㍢〱㠱扥扡攴昱㌸㘲㝣攸㉡戹ㅦ㑢收挵㜵扦㤲摦捤㔵昲㍢㤶挲昳〸㐵㕥㝦㤷㤲㜷㜵㤶㉣ㄷ攱㍤㈵昳㘲扣㤴㍣㔰㤷捣慢攳扡㘴㕥㕢てっ搲㈵搷〱攵㌷㕣㈵て㘶挹扣㕣敤㔷昲换戹㑡㝥挹㔲㜸ㅥ㙥挸㉢摡㔲昲㌰㘷挹㜲㔹摢㔳㌲㉦㙦㑢挹攵扡攴捤攰㜵挹扣㕡ㅤ愸搴㈵㑦〴捡捦戸㑡づ戳㘴㕥〰昶㉢昹㠹㕣㈵晦搵㔲㜸ㅥ㍢挸㙢挴㔲昲㜰㘷挹㜲愱搸㔳㌲㉦ㄸ㑢挹㈳㜴挹扣㠲慢㑢收昵摦挰㝥扡攴戱㌸挸㍤敡㉡㜹㌴㑢收㈵㔵扦㤲ㅦ捡㔵昲㠳㤶挲昳㐰㐰㕥㜵㤵㤲㈷㌸㑢㉥戱愵慥㤳㑦㕥㠲㤵㤲㈷改㤲㝢㠳搷㈵昳㡡㙡㘰㡡㉥㜹っづ㜲昷戸㑡㥥捡㤲户㠵㠹㕦挹户攷㉡昹㌶㑢攱㜹㔴㕦ㅦ㐴㤲㤲㘷㍡㑢㤶㡢㤹ㅥ㤴晢挲㔶㑡㥥慤㑢收㔵㐶㕤㜲㝦扣ぢㅣ愴㑢ㅥ㠷ㅤ攳〶㔷挹㠷戰㘴㕥昶昳㉢㜹㕤慥㤲慦戱ㄴ㥥㠷攸昱捡愰㤴㝣愴戳攴㈱戶搴㠵㌲㉦ㄳ㑡挹㜳㜵挹攵攰㜵挹扣敡ㄷ㠸敢㤲挷攳攳㜷㠵慢攴㈴㑢慥㠱㠹㕦挹ㄷ攷㉡昹㈲㑢攱㜹扣摤㜰㐴㤲㤲㡦㜲㤶㉣ㄷ摣㍣㈸㡦㠰慤㤴摣愸㑢收㤵㌰㕤㌲慦愳〵㥡㜵挹ㄳ㔰昲戹慥㤲ㄷ戲㘴㕥㥡昲㉢㜹㜵慥㤲捦戴ㄴ搹て㥥ぢ㑤戱换㔸㡣戸挶㌱㈴㑢㐰㠲挵扣㜲攵㝢つ㐶㥥〴㌳㑣㍦㌲〳慢戴捣㌶ㄱ㤴㘲〳㡢㔳扣㌸搵㈳挵挵㕢愶㍣户㐳㥥㌶搶㔸挷㤵㘵㍤昱昴㡣搶〵㘶敢㔴㍣っ〶捦捣㤸搵搰㘴慤㕡挲㐳㘲昸ㄴ〳晢昹っ㠶㜰㕣ㄵㄸ㐸㑤㙦挵〳ㅢ扡愷㈶户攱㤱㌳挹㤲愶ㄹ戱㜴摡㙣㙤晥㉤慣㙥挴㔴ㄸ晥㠱㌲晣攸㠷㙡昸慥㔰攳搲戳散攷㌹㌸㥥慢搳㠱㠷晤㕣愵㐲㍥㜴攳搷慤㙤㤴挵戶㠵㙡ㄵ晡㉣㜷㜱㍥慢摣㔱㉥㜹攱㐱ㅥ㤸㉤挱㡥㉡愹ㄷ㡦㤴㌳㡥㘷㤷摢㔱㥣㤰㠲愲ㄹ㘸㜵扥㡢㜴㍣挳攸摥㔴ㅦ㙢㙤㡤㉤㉤㘹慡㙦㌴㥢攷愵攷㤷搴㉦挶㔵㐹㍣挰〷挱㑡㑡㑡㡣㘵昸㥦ㄹ昸ちㅤ㘴敦㔵㈷㌲搵㜲㤲ㄵ㈰㐱㜵〸ㄴ摣戳慣㜲㑦昰㉤昷㘴㌱捤㤴㝢ち摤摢ㄱ㔶㤷慢づ㠷㍦㑢㌶㑥㠵㈲㤳㤲ㄷ戵攴昳㜴ㅡ捤㑦㈷㌹〳㈴愸㜸〵换㤱㌲敤㥢昲㉣㌱捤愴晣㍤摤ㅤ㈹攷摢㈹捦㠱㈲㤳㤲ㄷ愵㈴攵戹㌴㍦㡦攴㝣㤰愰㕡攸㑥戹挰㌷攵㠵㘲㥡㐹㜹ㄱ摤ㅤ㈹搳㜶捡㑢愰挸愴㍣搶㑥㜹㈹捤㉦㈳戹ㅣ㈴愸㡥㜷愷㡣晢愶㕣㈳愶㤹㤴㙢改敥㐸挹换㑡〲散搵㔰㘴㔲昲愲㤰㙣攵㌵㌴㕦㐷㜲㉤㐸㔰㥤收㑥㜹愸㙦捡敢挵㌴㤳昲〶扡㍢㔲慥戶㔳摥〴㐵㈶㈵㉦敡㐸捡㥢㘹㝥ぢ挹慤㈰㐱㜵㠱㍢攵っ摦㤴㜷㠸㘹㈶攵㥤㜴㜷愴扣搸㑥㜹㌷ㄴ㤹㤴扣㈸㈳㈹敦愱昹扤㈴昷㠱〴ㄵ慦挰㌸㜶㥦㠹扥㈹搷㡢㘹㈶攵㠳㜴㜷愴攴㘵ㄹ〱昶㘱㈸㌲㈹㜹㔱㐵㔲晥㠹收㡦㠸て㐸㔰摤散㑥戹㥦㙦捡㍦㡢㘹㈶攵㘳攲㕥㘰攵㉤㔰户摢㈹ㅦ㠷㈲㤳㤲ㄷ㐵㈴攵㕦㘹晥〴挹㤳㈰㐱㜵扦㍢㘵戵㙦捡㡤㘲㥡㐹昹っ摤ㅤ㕢昹㤰㥤昲㌹㈸㌲㈹㜹㔱㐳㔲㍥㑦昳ㄷ㐸㕥〴〹㉡㕥挱㜰〰扢㤷㙦捡㔷挴㌴㤳昲㔵扡㍢㔲㍥㘱愷㝣ㅤ㡡㑣㑡㕥㤴㤰㤴㙦搰晣㑤㤲㑤㈰㐱昵扣㍢攵㙥扥㈹摦ㄶ搳㑣捡㜷攸敥㐸昹戲㥤昲㍤㈸㌲㈹㜹㔱㐱㔲扥㑦昳扦㤳㝣〰ㄲ㔴㙦戹㔳昶昵㑤昹戱㤸㘶㔲㝥㐲㜷㐷㑡㕥㔶㤰摤攷㔳㈸㌲㈹㜹㔱㐰㔲㝥㐶昳捤㈴㥦㠳〴搵㈷敥㤴㕢昹愶晣㔲㑣㌳㈹扦愲扢㈳攵㘶㍢攵扦愰挸愴攴愰㕥㔲㝥㐳昳㝦㤳㝣ぢㄲ㔴摦戸㔳㤶昸愶晣㐱㑣㌳㈹㝦愴扢㈳攵昷㜶捡晦㐲㤱㐹挹㐱戹愴晣㠹收㍦㤳晣〲㠲攷㤱㠰㍡㜶㥦㕦扥昳晢攲㉢㉣愱㘹㈶㘵㌷戰捥㤴㐵㠸㈱挰ㄶ㐳㤱㐹ㄹ㠴㔴㔲〶㘸摥㥤愴〴㈴愸㝡扡㔳㝥敢㥢戲㠷㤸㘶㔲昶愴扢㘳㉢㐳㜶捡摥㔰㘴㔲㙥㙦愷㉣愵㜹㠸㘴㉢㤰愰攲〸搸戱㤵㥦晢愶摣㔶㑣㌳㈹户愳扢㈳㘵㍦㍢攵づ㔰㘴㔲㜲㔰㉢㕢搹㠷收㍢㤲昴〵〹慡㠱敥㤴ㅦ昸愶摣㔹㑣㌳㈹晢搳摤㤱㜲戰㥤戲っ㡡㑣捡㘱㜶捡〱㌴摦㤵㘴㌷㤰愰㉡㜷愷摣攴㥢㜲㤰㤸㘶㔲敥㐱㜷㐷㑡づ㑢愵㤷㝢㐲㤱㐹㌹摣㑥㌹㠴收㐳㐹昶〲〹慡ㄱ敥㤴㉦晡愶摣㐷㑣㌳㈹换改敥㐸㌹摡㑥㔹〹㐵㈶㈵〷㠵〲㙣ㄵ捤挳㈴搵㈰㐱㌵挹㥤昲㐹摦㤴ㄱ㌱捤愴㡣搲摤㤱㜲慡㥤㜲㕦㈸㌲㈹㌹愸㤳㤴㈳㘸㍥㤲㘴㍦㤰愰攲〸捥戱晢戴晢愶ㅣ㈳愶㤹㤴㘳改敥㐸挹㘱㥤〰㍢づ㡡㑣捡㈳敤㤴攳㘹㍥㠱㘴㈲㐸㔰捤㜵愷扣捦㌷攵ㄴ㌱捤愴摣㥦敥㡥㤴㐹㍢攵〱㔰㘴㔲㜲㔰㈵㕢㌹㡤收搳㐹㘶㠰〴㔵愳㍢攵慤扥㈹㘷㠹㘹㈶攵㙣扡㍢㔲㉥戴㔳ㅥ〴㠵㥤戲㜸㌱愴晢晡摤敤搶㠳㈰挷㥦㔳ㄸ㡡扦昸㠱愷㕡㥡㐹㡣㘳ㄶ攲慥昹搲昱捤改搶愵っ搴つ捦㤹㉢㤶㝢攲㐵㠵挳㝦㕤㉣㡥㠶㜶㐶㈸扥㡡㙦挰收晤㝦挴攱昸戴攳㘶㌹㈳㡥挰慢愴㌰愰㌸昸攳〶慢敢㤱㠱㔹㐶㡡㐲㈹づ〸㐵昱㐷㑢㌱ちち攳㌰〰㔵捣㤱㐵愷㠷㌸㑣晤㉢晦ち捡敦㤰㑣ㅤ捦攲㤸晡㜰㜲㜸挳㔷改㌲㑢㕡挲㘱㡡㍡搱慥昵ㅡ慢㔶㝢敢㤶摢㡡慢戳戶㡥〳ㄳ搹扡慢㥣㕢㌷㤷㈹㑥㠶㡡㕢㘸挴挸㜱ㅣ㈲改攳捥昴ㅣ㠴㔰慡搳㥦〶㑥㠲㕤㤱㤵㥥〳ㄲ㔱㕣㥥㤵㥥㠳ㄴ㔱㕣收㑣㥦㘲ちづ㑡㈴晤㍣㜲ㅣ㤳㐸晡昹捥昴攷㔸㔲㥤㥥〳ㄱ〹㜶㔱㔶㝡づ㑥㐴㜱㘱㔶㝡づ㔸㐴昱〷㘷晡㐶愶戸㄰㉡㐹摦㐴㡥攳ㄳ㐹摦散㑣捦挱㐹挷搶㕦㙡〷㍢㌷㉢晤㘵戶攲㥣慣昴㤷摢㡡戳㥤改㕢㤹㘲つ㔴㤲扥㡤摣㕡㜰㤲㍥敤㑣捦㠱㑡㐷㝡づ㔰㘴㕢捥捣㑡扦捥㔶㥣㤱㤵㥥〳ㄹ昱㌸摤㤹㝥〹㔳㕣て㤵愴㕦㑡㡥攳ㄶ㐹㝦慣㌳㍤〷㉤ㅤ改㙦戶㠳㥤㤲㤵㥥〳ㄸ挹㜲㜲㔶㝡づ㙡㐴㜱㤲㌳晤㌲愶攰㈰㐶搲㥦㐸㡥㘳ㄸ㐹扦摣㤹㥥〳㤸㡥昴ㅣ戸㐸戰ㄳ戳搲摦㙢㉢㤶㘵愵攷〰㐷㍣㑥㜰愶㍦㤹㈹搶㐳㈵改㑦㈱昷㈰㌸㐹扦捡㤹㥥㠳㤹㡥昴㝦戲㠳㉤捤㑡晦㠸慤㔸㤲㤵扥摤㔶ㅣ攳㑣㝦〶㔳㜰㜰㈳改捦㈴昷ㄸ㌸㐹扦摡㤹㥥〳㥢㡥昴ㅣ搰挸戶戴㘵愵㝦挲㔶戴㘶愵攷挰㐷㍣㡥㜶愶㍦㠷㈹㌶㐲㈵改捦㈵挷㜱㡥愴㍦捦㤹㥥㠳㥣㡥昴捦摢挱㥡戲搲㜳挰㈳㔹ㅡ戳搲㜳㄰㈴㡡〵捥昴ㄷ㌲〵〷㍤㤲晥㈲㜲慦㠲㤳昴ㄷ㍢搳㜳挰搳㤱㥥〳ㅤ〹㌶㉦㉢晤㥢戶㈲㤵㤵㝥㤳慤㌰㥤改㉦㘷㡡户愱㤲昴㔷㤰㝢〷㥣愴扦搲㤹㥥㠳㥦㡥昴ㅣ昴㐸晡㔸㔶㝡づ㠴㐴㌱㌷㉢晤〷戶愲摥㤹晥㙡愶攰㘰㐸搲㕦㐳敥ㄳ㜰㤲㝥㥤㌳㍤〷㐲ㅤ改㌹〰㤲㉣扦换㑡扦搹㔶ㅣ㤶㤵㥥〳㈵昱㌸搴㤹晥㝡愶昸ㄲ㉡㐹㝦〳㌹㡥㡢㈴晤㡤捥昴ㅣㄴ㜵愴攷㘰㐸㠲捤挹㑡捦〱㤲㈸㘶㘷愵晦搶㔶捣㜲愶扦㤵㈹㌸㐸㤲昴户㤱晢ㄱ㥣愴扦摤㤹晥扦㤶㔴ㅦ昳㌹㌰㤲㉣搳戳搲晦㙣㉢愶㘵愵晦挵㔶ㅣ攰㑣㝦㌷㔳ㄴ㠲㐸晡㝢挸㜱扣㈴改敦戵摥㤰㈹攵㘰愹㘳敢〳攰㈴晤攴慣昴ㅣ㌸㠹㘲㔲㔶㝡づ愶㐴㌱搱㤹㝥㍤愳㜲昰㈴改ㅦ㈴挷戱㤳愴㝦挸㝡㈳改㌹㜰敡㐸捦〱㤳〴慢换㑡ㅦ戲ㄵ㘳戳搲㜳㘰㈵ㅥ㘳㥣改摢ㄹ㜵㕢㄰㐹晦㈸㌹㡥愳㈴晤〶敢㡤愴攷㈰慡㈳㍤〷㑦ㄲ㙣㘴㔶㝡づ愸㐴㌱㈲㉢㍤〷㔹愲搸搷㤹晥㜱㐶攵愰㑡搲晦㤵ㅣ挷㔴㤲晥〹敢㡤愴攷㠰慡㈳㍤〷㔲ㄲ慣㌶㉢晤慥戶愲㈶㉢㍤〷㕣攲㔱敤㑣扦㤱㔱〷㠱㐸晡㘷挸敤㐱㠲㜶ㅢ捦㕡㙦㈴㍤〷㔷ㅤ改㌹愸㤲㘰ㄵ㔹改㌹搰ㄲ㐵㜹㔶晡扤㙣挵㍥捥昴㉦㌲㉡〷㕢㤲晥㈵㜲攵㈴㑣晦戲昵㐶搲㜳愰搵㤱㥥〳㉣挹㌲㌴㉢㝤搸㔶っ挹㑡捦㠱㤸㜸散改㑣晦㍡愳㐶㐰㈴晤ㅢ攴㌸敥㤲昴㙦㕡㙦㈴㍤〷㕤ㅤ改㌹搸㤲㘰扢㘷愵攷〰㑣ㄴ〳戳搲㜳㔰㈶㡡摤㥣改摦㘶㔴づ挲㈴晤㍢攴挶㤲㜰敢摦戵摥㐸㝡づ挰㍡搲㜳攰㈵挱㜶挹㑡㍦挱㔶昴捦㑡㍦搱㔶散散㑣晦〱愳㜲㐰㈶改㍦㈴挷昱㤸愴晦挸㝡㈳改㌹ㄸ敢㐸㍦つ㥣愴摦㌱㉢㍤〷㘶愲攸㤳㤵㝥㠶慤搸挱㤹晥㔳㐶攵攰㑣搲㝦㐶㙥㌶〹户㝥戳昵㐶搲㜳㘰㤶㐹㕦㝡ㄸ戸㠳㘱㔳戸㐴㈵收㈶攷捥晤扥戴愸慣㙦搱㈱愳㝢㕥昲敥㔳敦㥦昷昲攱㈳㍦晥敦攵㤷扦晣挱㜹ㅢ晦晢㔰㝣攴㕦慦扥晡戱㈹㙢㌶扥扦㜵㙡㙤攱扤摦㑦㕤㝢㝣挵㠲攳㡦㑥捤ㄹ㌲昱昸㐳㡦㍡戰㘲挶㔶㐳扢㜵敢摥㝤㡦㙤㥥攸㌳㌸戴晣攸晢搵愳㙦散搰慣㘴挴挱㈲㕣㌷ㅡ㌹昲㤰㌱攸ㄷ㜸搳慢㕢改摣慥㉥㐳㐶ㅥ㥥㌲攲㜶ㄹ㕦敡㌲㔲㕤㕤挶㍣㈴㤰㤶戸搰攰㐸㐴搰昸㕡㤷搱搸搵㘵挸㐸挴㠳㐶戳㕤挶㌷扡㡣搶慥㉥㐳㐶㈴㥥㌲搲㜶ㄹ摦敡㌲㤶㜴㜵ㄹ㌲㌲昱㤴㜱慣㕤挶昷扡㡣㘵㕤㕤㠶㡣㔰㍣㘵㉣户换昸㔱㤷挱㘱㐵㤷㝥㘰㘵愴攲㈹㘳㤵㕤挶㝦㜵ㄹ㘷㜴㜵ㄹ㘷㈲㠱昷㤳戲摡㉥攳㘷㕤挶㌹㕤㕤㠶㡣㕣㍣㘸㥣㘷㤷㔱㘰挸攱㡢挳㡤㉥㙤㡡㡣㘰㍣㘵㕣㙣㤷㔱愸换戸扣慢换㤰㤱㡣愷㡣㉢敤㌲㡡㜴ㄹ㔷㜷㜵ㄹ㌲愲昱㤴挱㤱㡤ㅣ㐵〳扡っづ㐳扡戴㈹㌲戲昱㤴㜱愳㕤㐶㠹㉥攳搶慥㉥㐳㐶㌸㥥㌲㙥户换〸敡㌲敥敥敡㌲㘴愴攳㈹㠳㈳ㅥ㘹㑡㑦㕤挶晡慥㉥㐳㐶㍣㥥㌲ㅥ戲换攸慤换㘸敦敡㌲㘴攴攳㈹㘳㠳㕤㐶㐸㤷昱㜸㔷㤷㈱㈳㈰㑦ㄹㅣ〹㐹㔳戶搶㘵㙣散敡㌲㘴㈴攴㈹攳㔹扢㡣㙤㜵ㄹ㉦㜶㜵ㄹ㌲㈲昲㤴昱戲㕤挶昶扡㡣搷扢扡っㄹㄹ㜹捡㜸搳㉥愳㡦㉥㠳挳㤹㉥㍤㝣挹〸挹㔳〶㐷㑡戲㙦昴搵㘵㜰㔸搳愵㘵挸㐸挹㔳〶㐷㑣㔲㐶㍦㕤〶㠷㌷㕤㕡㠶㡣㤸㍣㘵㜰攴㈴㘵昴㤷㌲ㄴ㠷㉢㌲㈸㝢敦㕢㝤㙦㘷㉣㕣㑡昰㈴〸づ㈰㐴昱㙥㤶㠲愷昴愲㜸㈷㑢挱㤳㙣㔱扣㥤愵攰㘹慦㈸晥㤶愵攰㠹愸㈸摥捡㔲昰搴㔰ㄴ㥢戲ㄴ㍣㔹ㄳ挵㥢㔹ち㥥㍥㠹攲㡤㉣〵㑦㘸㐴昱㝡㤶㠲愷ㄸ愲㜸㉤㑢挱㉦㝤㔱扣㥡愵攰搷戰㈸㕥挹㔲昰㡢㔱ㄴ㉦㘷㈹昸㔵㈵㡡㤷戲ㄴ晣昲㄰挵㡢㔹ちㅥ捥㐵昱㐲㤶㠲〷㔸㔱㍣㥦愵攰㈱㑦ㄴ捦㘵㈹㜸㄰ㄲ挵戳㔹ちㅥㄶ㐴昱㑣㤶㠲ㅦ㔴㔱㙣捣㔲昰愳㈳㡡愷戳ㄴ摣㤹㐵昱㔴㤶㠲扢㤷㈸㥥㜴㉢㝡晣㍦㜱㘶づ㙤
[9 empty] | Decisioneering:7.0.0.0 | Decisioneering:7.0.0.0 | [5 empty] | Decisioneering:7.0.0.0 | Decisioneering:7.0.0.0

## Pathways Stage3
PATHWAY SUMMARY
Stage 3
Path 1 |  | Section 1 |  | Section 2 |  | Section 3
Path 1 Type |  | Source |  | Unit |  | Receptor
Path 1 Name |  | Phase1 |  | CollierySpoil: Node 1 |  | WaterTable
Path 1 Process |  | Declining source |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 1 Standards |  |  |  |  | Target Standard | MRV
Path 1 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 1.2459e-07
Path 1 Parameter2 | Managed time [years] | 7 | Dispersivity [m] | 5
Path 1 Parameter3 | Q_path [m3/s] | 0.0001163 | Travel Distance [m] | 50
Path 1 Parameter4 | Q_decline [m3/s] | 0.0001163 | Mixing Depth [m]
Path 1 Parameter5 |  |  | Mixing Width [m]
Path 1 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_dilute [m3/s] | 0
Path 2 |  | Section 1 |  | Section 2 |  | Section 3 |  | Section 4
Path 2 Type |  | Source |  | Unit |  | Unit |  | Receptor
Path 2 Name |  | Phase1 |  | CollierySpoil: Node 1 |  | CoalMeasures: Node 1 |  | SiteEdge
Path 2 Process |  | Declining source |  | ADRD (1D) + Dilution |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 2 Standards | [6 empty] | Target Standard | DWS/EQS
Path 2 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 1.2459e-07 | Velocity [m/s] | 1.3333e-06
Path 2 Parameter2 | Managed time [years] | 7 | Dispersivity [m] | 5 | Dispersivity [m] | 35
Path 2 Parameter3 | Q_path [m3/s] | 0.0001163 | Travel Distance [m] | 50 | Travel Distance [m] | 350
Path 2 Parameter4 | Q_decline [m3/s] | 0.0001163 | Mixing Depth [m] |  | Mixing Depth [m] | 5
Path 2 Parameter5 |  |  | Mixing Width [m] |  | Mixing Width [m] | 0
Path 2 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_Dilute [m3/s] | 0 | Q_dilute [m3/s] | 0
Path 3 |  | Section 1 |  | Section 2 |  | Section 3
Path 3 Type |  | Source |  | Unit |  | Receptor
Path 3 Name |  | MerthyrWaste |  | CollierySpoil: Node 2 |  | WaterTable
Path 3 Process |  | Declining source |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 3 Standards |  |  |  |  | Target Standard | MRV
Path 3 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 8.1654e-07
Path 3 Parameter2 | Managed time [years] | 0 | Dispersivity [m] | 5
Path 3 Parameter3 | Q_path [m3/s] | 0.00010307 | Travel Distance [m] | 50
Path 3 Parameter4 | Q_decline [m3/s] | 0.00010307 | Mixing Depth [m]
Path 3 Parameter5 |  |  | Mixing Width [m]
Path 3 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_dilute [m3/s] | 0
Path 4 |  | Section 1 |  | Section 2 |  | Section 3 |  | Section 4
Path 4 Type |  | Source |  | Unit |  | Unit |  | Receptor
Path 4 Name |  | MerthyrWaste |  | CollierySpoil: Node 2 |  | CoalMeasures: Node 2 |  | SiteEdge
Path 4 Process |  | Declining source |  | ADRD (1D) + Dilution |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 4 Standards | [6 empty] | Target Standard | DWS/EQS
Path 4 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 8.1654e-07 | Velocity [m/s] | 1.3333e-06
Path 4 Parameter2 | Managed time [years] | 0 | Dispersivity [m] | 5 | Dispersivity [m] | 35
Path 4 Parameter3 | Q_path [m3/s] | 0.00010307 | Travel Distance [m] | 50 | Travel Distance [m] | 350
Path 4 Parameter4 | Q_decline [m3/s] | 0.00010307 | Mixing Depth [m] |  | Mixing Depth [m] | 5
Path 4 Parameter5 |  |  | Mixing Width [m] |  | Mixing Width [m] | 400
Path 4 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_Dilute [m3/s] | 0.0006 | Q_dilute [m3/s] | 0
Path 5 |  | Section 1 |  | Section 2 |  | Section 3
Path 5 Type |  | Source |  | Unit |  | Receptor
Path 5 Name |  | Phase2to6 |  | CollierySpoil: Node 3 |  | WaterTable
Path 5 Process |  | Declining source |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 5 Standards |  |  |  |  | Target Standard | MRV
Path 5 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 8.1654e-07
Path 5 Parameter2 | Managed time [years] | 7 | Dispersivity [m] | 5
Path 5 Parameter3 | Q_path [m3/s] | 0.0012516 | Travel Distance [m] | 50
Path 5 Parameter4 | Q_decline [m3/s] | 0.0012516 | Mixing Depth [m]
Path 5 Parameter5 |  |  | Mixing Width [m]
Path 5 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_dilute [m3/s] | 0
Path 6 |  | Section 1 |  | Section 2 |  | Section 3 |  | Section 4
Path 6 Type |  | Source |  | Unit |  | Unit |  | Receptor
Path 6 Name |  | Phase2to6 |  | CollierySpoil: Node 3 |  | CoalMeasures: Node 3 |  | SiteEdge
Path 6 Process |  | Declining source |  | ADRD (1D) + Dilution |  | ADRD (1D) + Dilution |  | Monitoring Borehole
Path 6 Standards | [6 empty] | Target Standard | DWS/EQS
Path 6 Parameter1 | Q_managed [m3/s] | 0 | Velocity [m/s] | 8.1654e-07 | Velocity [m/s] | 1.3333e-06
Path 6 Parameter2 | Managed time [years] | 7 | Dispersivity [m] | 5 | Dispersivity [m] | 35
Path 6 Parameter3 | Q_path [m3/s] | 0.0012516 | Travel Distance [m] | 50 | Travel Distance [m] | 350
Path 6 Parameter4 | Q_decline [m3/s] | 0.0012516 | Mixing Depth [m] |  | Mixing Depth [m] | 5
Path 6 Parameter5 |  |  | Mixing Width [m] |  | Mixing Width [m] | 0
Path 6 Parameter6 |  |  | Q_Dilute [m3/s] | 0 | Q_Dilute [m3/s] | 0 | Q_dilute [m3/s] | 0

## TransProb Results
Transient Probabilistic Results |  |  |  |  | #NAME? | Monte Carlo iterations
Site Name: "Trecatti"
Advanced
Pollutant Linkage: Phase1, CollierySpoil, WaterTable | [7 empty] | Pollutant Linkage: Phase1, CollierySpoil, CoalMeasures, SiteEdge | [7 empty] | Pollutant Linkage: MerthyrWaste, CollierySpoil, WaterTable | [7 empty] | Pollutant Linkage: MerthyrWaste, CollierySpoil, CoalMeasures, SiteEdge | [7 empty] | Pollutant Linkage: Phase2to6, CollierySpoil, WaterTable | [7 empty] | Pollutant Linkage: Phase2to6, CollierySpoil, CoalMeasures, SiteEdge
50 | th Percentile Concentrations in mg/L in WaterTable | [6 empty] | 50 | th Percentile Concentrations in mg/L in SiteEdge | [6 empty] | 50 | th Percentile Concentrations in mg/L in WaterTable | [6 empty] | 50 | th Percentile Concentrations in mg/L in SiteEdge | [6 empty] | 50 | th Percentile Concentrations in mg/L in WaterTable | [6 empty] | 50 | th Percentile Concentrations in mg/L in SiteEdge
Compared with MRV target concentration in mg/L | [7 empty] | Compared with DWS/EQS target concentration in mg/L | [7 empty] | Compared with MRV target concentration in mg/L | [7 empty] | Compared with DWS/EQS target concentration in mg/L | [7 empty] | Compared with MRV target concentration in mg/L | [7 empty] | Compared with DWS/EQS target concentration in mg/L
| 0 | 0 | 0.0001 | 0.0001 | 0.004 | 0 | 0.003 |  | 250 | 0.39 | 0.0001 | 0.005 | 0.05 | 0.0001 | 0.03 |  | 0 | 0 | 0.0001 | 0.0001 | 0.004 | 0 | 0.003 |  | 250 | 0.39 | 0.0001 | 0.005 | 0.05 | 0.0001 | 0.03 |  | 0 | 0 | 0.0001 | 0.0001 | 0.004 | 0 | 0.003 |  | 250 | 0.39 | 0.0001 | 0.005 | 0.05 | 0.0001 | 0.03
Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7 | Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7 | Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7 | Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7 | Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7 | Time(years) | Species1 | Species2 | Species3 | Species4 | Species5 | Species6 | Species7
| Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene |  | Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene |  | Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene |  | Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene |  | Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene |  | Chloride | Ammoniacal_N | Mecoprop | Cadmium | Toluene | Naphthalene | Xylene
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
#REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #REF! | 0 | 0 | 0 | 0 | 0 | 0 | 0
end of data | [47 empty] | end of data

## TransCalcs
TRANSIENT CALCULATIONS
Path 1 Parameters | [26 empty] | Path 2 Parameters | [26 empty] | Path 3 Parameters | [26 empty] | Path 4 Parameters | [26 empty] | Path 5 Parameters | [26 empty] | Path 6 Parameters
|  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8 |  |  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8 |  |  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8 |  |  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8 |  |  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8 |  |  |  | Species 1 | Species 1 | Species 1 | Species 2 | Species 2 | Species 2 | Species 3 | Species 3 | Species 3 | Species 4 | Species 4 | Species 4 | Species 5 | Species 5 | Species 5 | Species 6 | Species 6 | Species 6 | Species 7 | Species 7 | Species 7 | Species 8 | Species 8 | Species 8
|  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 |  |  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 |  |  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 |  |  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 |  |  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 |  |  |  | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3 | Stage 1 | Stage 2 | Stage 3
|  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined |  |  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined |  |  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined |  |  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined |  |  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined |  |  |  | Chloride | Chloride | Chloride | Ammoniacal_N | Ammoniacal_N | Ammoniacal_N | Mecoprop | Mecoprop | Mecoprop | Cadmium | Cadmium | Cadmium | Toluene | Toluene | Toluene | Naphthalene | Naphthalene | Naphthalene | Xylene | Xylene | Xylene | Undefined | Undefined | Undefined
Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Source |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | numparam |  |  | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11
krel |  |  | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | #DIV/0! | #DIV/0! | #DIV/0! | krel |  |  | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | 1.7742e-09 | 1.8371e-12 | 1.0022e-09 | #DIV/0! | #DIV/0! | #DIV/0! | krel |  |  | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | #DIV/0! | #DIV/0! | #DIV/0! | krel |  |  | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | #DIV/0! | #DIV/0! | #DIV/0! | krel |  |  | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | #DIV/0! | #DIV/0! | #DIV/0! | krel |  |  | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | 1.1597e-09 | 1.2007e-12 | 6.5506e-10 | #DIV/0! | #DIV/0! | #DIV/0!
kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0! | kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0! | kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0! | kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0! | kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0! | kmgd |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | #DIV/0! | #DIV/0! | #DIV/0!
M0 |  |  | 490765.5455 | 490765.5455 | 490765.5455 | 232559.5065 | 232559.5065 | 232559.5065 | 6.2318 | 6.2318 | 6.2318 | 0.090517 | 0.090517 | 0.090517 | 4.7347 | 4.7347 | 4.7347 | 12.3011 | 12.3011 | 12.3011 | 5.5239 | 5.5239 | 5.5239 | 0 | 0 | 0 | M0 |  |  | 490765.5455 | 490765.5455 | 490765.5455 | 232559.5065 | 232559.5065 | 232559.5065 | 6.2318 | 6.2318 | 6.2318 | 0.090517 | 0.090517 | 0.090517 | 4.7347 | 4.7347 | 4.7347 | 12.3011 | 12.3011 | 12.3011 | 5.5239 | 5.5239 | 5.5239 | 0 | 0 | 0 | M0 |  |  | 2270000 | 2270000 | 2270000 | 723000 | 723000 | 723000 | 78.7 | 78.7 | 78.7 | 10.1 | 10.1 | 10.1 | 57.6 | 57.6 | 57.6 | 111.6 | 111.6 | 111.6 | 19.5 | 19.5 | 19.5 | 0 | 0 | 0 | M0 |  |  | 2270000 | 2270000 | 2270000 | 723000 | 723000 | 723000 | 78.7 | 78.7 | 78.7 | 10.1 | 10.1 | 10.1 | 57.6 | 57.6 | 57.6 | 111.6 | 111.6 | 111.6 | 19.5 | 19.5 | 19.5 | 0 | 0 | 0 | M0 |  |  | 8079904.0618 | 8079904.0618 | 8079904.0618 | 3828831.3407 | 3828831.3407 | 3828831.3407 | 102.5989 | 102.5989 | 102.5989 | 1.4903 | 1.4903 | 1.4903 | 77.9523 | 77.9523 | 77.9523 | 202.523 | 202.523 | 202.523 | 90.9443 | 90.9443 | 90.9443 | 0 | 0 | 0 | M0 |  |  | 8079904.0618 | 8079904.0618 | 8079904.0618 | 3828831.3407 | 3828831.3407 | 3828831.3407 | 102.5989 | 102.5989 | 102.5989 | 1.4903 | 1.4903 | 1.4903 | 77.9523 | 77.9523 | 77.9523 | 202.523 | 202.523 | 202.523 | 90.9443 | 90.9443 | 90.9443 | 0 | 0 | 0
t0 |  |  | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | t0 |  |  | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | t0 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | t0 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | t0 |  |  | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | t0 |  |  | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200 | 220903200
kpath |  |  | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | #DIV/0! | #DIV/0! | #DIV/0! | kpath |  |  | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | 7.8204e-11 | 1.8371e-12 | 1.0022e-09 | #DIV/0! | #DIV/0! | #DIV/0! | kpath |  |  | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | #DIV/0! | #DIV/0! | #DIV/0! | kpath |  |  | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | 1.7787e-09 | 1.8824e-13 | 1.0307e-10 | #DIV/0! | #DIV/0! | #DIV/0! | kpath |  |  | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | #DIV/0! | #DIV/0! | #DIV/0! | kpath |  |  | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | 5.1116e-11 | 1.2007e-12 | 6.5506e-10 | #DIV/0! | #DIV/0! | #DIV/0!
csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | csol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | phi |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Vol |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
Velocity |  |  | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | Velocity |  |  | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | 4.6323e-08 | 2.0837e-08 | 1.2459e-07 | Velocity |  |  | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | Velocity |  |  | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | 1e-06 | 2.7324e-08 | 8.1654e-07 | Velocity |  |  | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | Velocity |  |  | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07 | 4.653e-08 | 2.7324e-08 | 8.1654e-07
Dispersivity |  |  | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5 | 5 | 5 | Dispersivity |  |  | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5.0432 | 5.096 | 5.0161 | 5 | 5 | 5 | Dispersivity |  |  | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5 | 5 | 5 | Dispersivity |  |  | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5.002 | 5.0732 | 5.0024 | 5 | 5 | 5 | Dispersivity |  |  | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5 | 5 | 5 | Dispersivity |  |  | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5.043 | 5.0732 | 5.0024 | 5 | 5 | 5
Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1 | Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1 | Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1 | Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1 | Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1 | Retard |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 312.04 | 312.04 | 312.04 | 2305 | 2305 | 2305 | 553.96 | 553.96 | 553.96 | 1 | 1 | 1
Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 7.3265e-09 | 7.3265e-09 | 7.3265e-09 | 7.6224e-08 | 7.6224e-08 | 7.6224e-08 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0
Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | Length |  |  | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | ADRD |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Velocity |  |  | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Velocity |  |  | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Velocity |  |  | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06 | 1.3333e-06
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Dispersivity |  |  | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35 | 35 | 35 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Dispersivity |  |  | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35 | 35 | 35 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Dispersivity |  |  | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35.0015 | 35 | 35 | 35
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Retard |  |  | 1 | 1 | 1 | 6.84 | 6.84 | 6.84 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 70.12 | 70.12 | 70.12 | 513 | 513 | 513 | 123.88 | 123.88 | 123.88 | 1 | 1 | 1 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Retard |  |  | 1 | 1 | 1 | 6.84 | 6.84 | 6.84 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 70.12 | 70.12 | 70.12 | 513 | 513 | 513 | 123.88 | 123.88 | 123.88 | 1 | 1 | 1 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Retard |  |  | 1 | 1 | 1 | 6.84 | 6.84 | 6.84 | 1 | 1 | 1 | 47857 | 47857 | 47857 | 70.12 | 70.12 | 70.12 | 513 | 513 | 513 | 123.88 | 123.88 | 123.88 | 1 | 1 | 1
9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Decay coeff |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.032e-08 | 6.032e-08 | 6.032e-08 | 5.6696e-08 | 5.6696e-08 | 5.6696e-08 | 2.9279e-08 | 2.9279e-08 | 2.9279e-08 | 0 | 0 | 0
9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Length |  |  | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 0.0017787 | 1.8824e-07 | 0.00010307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Length |  |  | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Length |  |  | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350
Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
W |  |  | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | W |  |  | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | W |  |  | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | 1.3373 | 3188.337 | 6.8214 | W |  |  | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0023787 | 0.00060019 | 0.00070307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
|  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0023787 | 0.00060019 | 0.00070307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[27 empty] | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | [27 empty] | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | [27 empty] | Dummy |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
|  | Calcs_DF_Path1 | 1 | 1 | 1 | [21 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 |  |  | Calcs_DF_Path3 | 1 | 1 | 1 | [21 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 |  |  | Calcs_DF_Path5 | 1 | 1 | 1 | [21 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
[27 empty] | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | [27 empty] | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | [27 empty] | W |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[27 empty] | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [27 empty] | 0.0023787 | 0.00060019 | 0.00070307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [27 empty] | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[27 empty] | 9.0754e-06 | 2.1319e-07 | 0.0001163 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [27 empty] | 0.0023787 | 0.00060019 | 0.00070307 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [27 empty] | 9.7661e-05 | 2.2941e-06 | 0.0012516 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[27 empty] | Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | [27 empty] | Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | [27 empty] | Conversion |  |  | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
[27 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | [27 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | [27 empty] | numparam |  |  | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
[27 empty] | W |  |  | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | 9.0754e-09 | 2.1319e-10 | 1.163e-07 | [27 empty] | W |  |  | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | 1.7787e-06 | 1.8824e-10 | 1.0307e-07 | [27 empty] | W |  |  | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06 | 9.7661e-08 | 2.2941e-09 | 1.2516e-06
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [30 empty] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
[29 empty] | Calcs_DF_Path2 | 1 | 1 | 1 | [50 empty] | Calcs_DF_Path4 | 1.3373 | 3188.337 | 6.8214 | [50 empty] | Calcs_DF_Path6 | 1 | 1 | 1

## Trans Parameters
TRANSIENT PARAMETERS
End of Stage 1 | 47 | Years | 1483207200
End of Stage 2 | 307 | Years | 9688183200
Duration of managed stage | 7 | Years
Pathway section parameters
| Path1Arr |  |  | Path2Arr |  |  | Path3Arr |  |  | Path4Arr |  |  | Path5Arr |  |  | Path6Arr
| Length (m) | Sections |  | Length (m) | Sections |  | Length (m) | Sections |  | Length (m) | Sections |  | Length (m) | Sections |  | Length (m) | Sections
CollierySpoil | 50 | 10 | CollierySpoil | 50 | 10 | CollierySpoil | 50 | 10 | CollierySpoil | 50 | 10 | CollierySpoil | 50 | 10 | CollierySpoil | 50 | 10
Extra length | 10 | 10 | CoalMeasures | 350 | 10 | Extra length | 10 | 10 | CoalMeasures | 350 | 10 | Extra length | 10 | 10 | CoalMeasures | 350 | 10
|  |  | Extra length | 10 | 10 |  |  |  | Extra length | 10 | 10 |  |  |  | Extra length | 10 | 10

## User Forecast
Checks Phase 1 |  |  |  |  | Percentile | 0 | 50 | 95 | 100 |  | 100
converge_chk | 1 |  |  | - |  | #NAME? | #NAME? | #NAME? | #NAME? |  | 95
| P1 | P234 | Pallsite |  |  | 100
Head level check | 0 | 0 | 0 | - |  | #NAME? | #NAME? | #NAME?
Converged base | 1 | 1 | 1 | - |  | #NAME? | #NAME? | #NAME?
Flows | [5 empty] | 100 |  |  |  | 95
heads | 10.0133 | 32.5911 | 0 | maod |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qover | 0 | 0 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qerror | 0 | 4.0658e-20 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
q_path | 9.0754e-06 | 9.7661e-05 | 0.00010674 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
v_path | 4.6323e-08 | 4.653e-08 | 4.6513e-08 | m/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
[6 empty] | 100 |  |  |  | 95
q_path MW | 0.0017787 | m3/s |  |  |  | #NAME? |  |  |  | #NAME?
Areas |  |  |  |  | Percentile | 0 | 50 | 95 | 100
Slope check | 0.98395 |  |  |  |  | #NAME? | #NAME? | #NAME? | #NAME?
Checks Phase 2 |  |  |  |  | Percentile | 0 | 50 | 95 | 100
converge_chk | 1 |  |  | - |  | #NAME? | #NAME? | #NAME? | #NAME?
| P1 | P234 | Pallsite |  |  | 100
Head level check | 0 | 0 | 0 | - |  | #NAME? | #NAME? | #NAME?
Converged base | 1 | 1 | 1 | - |  | #NAME? | #NAME? | #NAME?
Flows | [5 empty] | 100 |  |  |  | 95
heads | 0.56576 | 6.4224 | 0 | maod |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qover | 0 | 0 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qerror | 0 | 0 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
q_path | 2.1319e-07 | 2.2941e-06 | 2.5073e-06 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
v_path | 2.0837e-08 | 2.7324e-08 | 2.662e-08 | m/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
[6 empty] | 100 |  |  |  | 95
q_path MW | 1.8824e-07 | m3/s |  |  |  | #NAME? |  |  |  | #NAME?
q_pump | 0 | m3/s | 0 | m3/d |  | #NAME? |  | #NAME? |  | #NAME? |  | #NAME?
Areas |  |  |  |  | Percentile | 0 | 50 | 95 | 100
Slope check | 0.14775 |  |  |  |  | #NAME? | #NAME? | #NAME? | #NAME?
Checks Phase 3 |  |  |  |  | Percentile | 0 | 50 | 95 | 100
converge_chk | 1 |  |  | - |  | #NAME? | #NAME? | #NAME? | #NAME?
| P1 | P234 | Pallsite |  |  | 100
Head level check | 0 | 0 | 0 | - |  | #NAME? | #NAME? | #NAME?
Converged base | 1 | 1 | 1 | - |  | #NAME? | #NAME? | #NAME?
Flows | [5 empty] | 100 |  |  |  | 95
heads | 4.0925 | 13.3152 | 17.4041 | maod |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qover | 0 | 0 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
Qerror | -4.0658e-20 | 0 | 0 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
q_path | 0.0001163 | 0.0012516 | 0.0013679 | m3/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
v_path | 1.2459e-07 | 8.1654e-07 | 5.5463e-07 | m/s |  | #NAME? | #NAME? | #NAME? |  | #NAME? | #NAME? | #NAME?
[6 empty] | 100 |  |  |  | 95
q_path MW | 0.00010307 | m3/s |  |  |  | #NAME? |  |  |  | #NAME?
q_pump | 0 | m3/s | 0 | m3/d |  | #NAME? |  | #NAME? |  | #NAME? |  | #NAME?
Areas |  |  |  |  | Percentile | 0 | 50 | 95 | 100
Slope check | 0.45286 |  |  |  |  | #NAME? | #NAME? | #NAME? | #NAME?

## SiteEdge (hidden)
RECEPTOR: SiteEdge
Receptor Options
No further dilution along pathway
No data requirement
Group Box 1
Monitoring Borehole
Abstraction Borehole
River
User defined Receptor

## WaterTable (hidden)
RECEPTOR: WaterTable
Receptor Options
No further dilution along pathway
No data requirement
Group Box 1
Monitoring Borehole
Abstraction Borehole
River
User defined Receptor