## Report
Biffa Waste Services
Trecatti Landfill Site
Annual Monitoring Review
January 2018 to December 2018
As required by condition 4.2.1 of Permit RP3733PC/V0010 for Trecatti Landfill, the operator is required to complete an annual review of monitoring data.
The annual review will be based upon the monitoring results that the permit requires the Operator to undertake, which for the purposes of this report will run from January 2018 to December 2018. Biffa's monitoring is either carried out by ourselves, Lucideon or ALS laboratories. Biogene' surface water testing is carried out by Chemtest.
The review is split into 6 sections;
1. Surface Water
2. Leachate/Treated Effluent
3. Groundwater
4. Landfill Gas
5. Dust and Asbestos monitoring
6. Biogene
Capacity at Trecatti
Between July 2017 – July 2018, 166,527m3 of void has been consumed, with the remaining void in July 2018 calculated as approximately 5,810,987m3 for the site to be completed to final levels. An assessment of the settlement behaviour on a site such as Trecatti is extremely difficult as the majority of the site has accepted waste in the last 12 months. The area of the site that has been restored to final level appears to show no expedient settlement and continues to settle in a uniform manner.
1. Surface Water
The permit requires surface water discharge to be sampled and recorded monthly and to test for the following contaminants:
pH / Suspended Solids / Ammoniacal Nitrogen / COD
Following an Environment Agency audit on surface water management carried out on 16th May 2008, and subsequently approved on 30th July 2008, the
monitoring points have been amended as follows:
· SWA (81702001) – North Western boundary downstream discharge point
· SWB (81702002) – Eastern boundary downstream discharge point
· SWC (81702003) – Northern boundary upstream monitoring point
· Monocell (81702014) - inside the engineered area
During the audit it was agreed that as the operator is unable to control the external influences on all four monitoring points that the rate of flow and volume
measurement limit requirements on all three points would be removed. However volume of surface water pumped off site to the discharge point SWA would
be reported
Between January 2018 and December 2018 approximately 26,148,047m3 of surface water was pumped off site.
The following results were recorded for the period:
Sample point 81702001 SWA |  | (Discharge)
Parameter | pH | Suspended Solids | Ammonical Nitrogen | COD | Sample point SWA - 81702001 breached the upper pH limit during May and June. A schedule 5 was Submitted along with the quarterly report for that period.
Permit Limit | 6-8 | 100 mg/l | 5 mg/l | 120 mg/l
2018-01-01 | 7.9 | 4 | 2.16 | 28
2018-02-01 | 8 | 4 | <0.41 | 35
2018-03-01 | 7.3 | 16 | 2.66 | 27
2018-04-01 | 7.9 | 36 | 1.62 | 32
2018-05-01 | 8.1 | 2 | <0.41 | 27
2018-06-01 | 8.1 | 10 | <0.41 | 39
2018-07-01 | Insufficient Flow
2018-08-01 | 7.6 | 10 | <0.41 | 19
2018-09-01 | 7.5 | 5 | 0.92 | 28
2018-10-01 | 7.7 | 2 | 0.64 | 35
2018-11-01 | 7.5 | 8 | 0.82 | 26
2018-12-01 | 7.9 | 19 | 2.04 | 18
Sample point 81702002 SWB |  | (Downstream)
Parameter | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit Limit | 6-8 | 100 mg/l | 5 mg/l | 120 mg/l
2018-01-01 | 8 | 4 | <0.41 | 29
2018-02-01 | 7.5 | 3 | <0.41 | 30
2018-03-01 | 7.6 | 38 | <0.41 | 25
2018-04-01 | 8 | 21 | <0.41 | 49
2018-05-01 | Insufficient Flow | [10 empty] | 4655
2018-06-01 | Insufficient Flow | [10 empty] | 3192
2018-07-01 | Insufficient Flow | [10 empty] | 5608
2018-08-01 | Insufficient Flow
2018-09-01 | 7.5 | 10 | <0.41 | 62
2018-10-01 | Insufficient Flow
2018-11-01 | 7.3 | 15 | <0.41 | 35
2018-12-01 | 7.2 | 12 | <0.41 | 37
Sample point 81702003 SWC |  | (Upstream)
Parameter | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit Limit | N/A | N/A | N/A | N/A
2018-01-01 | 7.7 | 2 | <0.41 | 46
2018-02-01 | 7.1 | 8 | <0.41 | 40
2018-03-01 | 6.9 | 7 | <0.41 | 33
2018-04-01 | 7.5 | 8 | 15.5 | 62
2018-05-01 | 7.2 | 7 | <0.41 | 49
2018-06-01 | Insufficent Sample
2018-07-01 | Insufficent Sample
2018-08-01 | Insufficent Sample
2018-09-01 | 7.5 | 4 | <0.41 | 13
2018-10-01 | Insufficent Sample
2018-11-01 | 7.3 | 5 | 0.44 | 49
2018-12-01 | 7.3 | 2 | <0.41 | 37
Sample point Monocell 81702014 (on site)
Parameter | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Asbestos Fibres
Permit Limit | 6-8 | 100mg/l | 5mg/l | 120mg/l | no detection
2018-01-01 | 7.7 | 20 | 2.77 | 107 | no detection
2018-02-01 | 6.9 | 6 | <0.41 | 23 | no detection
2018-03-01 | 7.4 | 33 | 1.75 | 28 | no detection
2018-04-01 | 7.9 | 7 | 1.41 | 48 | no detection
2018-05-01 | 8 | 8 | 1.69 | 29 | no detection
2018-06-01 | 7.9 | 8 | 0.53 | 56 | no detection
2018-07-01 | Insufficent Sample
2018-08-01 | 7.8 | 2 | 1.72 | 23 | no detection
2018-09-01 | 7.5 | 4 | <0.41 | 13 | no detection
2018-10-01 | 7.5 | 40 | 1.37 | 32 | no detection
2018-11-01 | 7.2 | 10 | 0.6 | 32 | no detection
2018-12-01 | 7.9 | 64 | <0.41 | 41 | no detection
· All permanent engineering works (lining and capping/restoration) will continue to consider the impact of the works on surface water management during the design, construction and post-construction stages. This will include the provision of temporary storage lagoons, bunds, rain-flaps, ditches and pumping stations and pipelines. All permanent construction work will be the subject of independent CQA supervision. · All temporary engineering works (temporary capping) will consider the impact of surface water and may require the construction of rain-flaps and lined ditches to shed uncontaminated surface water into perimeter drainage ditches or temporary storage lagoons. · In order to reduce the build up of suspended solids within surface water bodies and water courses, any bare soil flanks and restored areas will be seeded with a suitable grass mix as soon as practicable in order to stabilise flanks, encourage infiltration and reduce surface run-off. This will be inspected and reseeded if necessary. · Spot sampling will be undertaken by the ECA in the site laboratory prior to any surface water being pumped to the perimeter ditch. · V-notch weirs are installed upstream of the surface water discharge points in order to slow down the flow of water to encourage the settlement of suspended solids prior to discharge. These features will be cleaned and maintained on a quarterly basis, and recorded on the critical plant schedule. · Perimeter surface water ditches, lagoons and other site drainage outlets will be inspected on a weekly basis and recorded in the site diary. · Road sweeper to be employed a minimum of twice a week. On periods of increased activity or poor weather conditions a road sweeper will be used more frequently or when the wheel wash is non-operational for a long period. This is left to the manager’s discretion. · Site to have a fully operational wheel wash, which will be cleaned every six months. A spare wheel wash pump will be held at site to replace immediately if the current pump fails reducing down time. The wheel wash is part of the critical plant list, which is reviewed monthly to ensure it is maintained as per schedule. The wheel wash may be cleaned more frequently depending on the manager’s findings during his/her monthly compliance inspection. All site users driving vehicles are instructed that they must use this facility before leaving site. Persistent misuse of the wheel wash by lorry drivers will lead to the driver being banned. · All waste vehicles must be sheeted upon arrival at Trecatti. De-sheeting must only take place in designated de-sheeting bay. · Vehicle check areas must be used by all drivers before leaving site so they can clean any excessive debris off their vehicles and remove any stones which may have been caught within their tyres whilst travelling over site.
2. Leachate
Leachate wells
The permit requires the Operator to sample leachate quarterly for the following components;
pH / Ammoniacal Nitrogen / Chloride / Total Alkalinity / BOD / COD / TOC / TON / Iron / Chromium / Copper / Lead / Zinc / Nickel / Cadmium / Magnesium / Potassium /
Sulphate / Calcium / Sodium / Manganese / Mecoprop / Toulene / Xylene / Naphthalene.
The permit also requires an annual suite to include the parameters above and hazardous substances
Leachate was sampled in February 18, May 18 and August 18 and annual components analysed for in November 18. There are however no limits set up in the permit with which the leachate samples must comply, but they have been reviewed and are as expected.
The permit requires the operator to report leachate levels from specified points at monthly intervals. A summary of the monthly reported results is below;
| Leachate Well 1 (mAOD) | Leachate Well 2 (mAOD) | Leachate Well 3 (mAOD) | Leachate Well 4 (mAOD) | Leachate Well 5 (mAOD) | Leachate Well 6 (mAOD) | Leachate Well 7 (mAOD) | Leachate Well 8 (mAOD) | Rainfall Total (mm)
[11 empty] | Leachate Well |  | Dip to base (m)
2018-01-01 | 360.92 | 356.96 | 350.53 | 361.09 | 373.04 | 376.48 | 369.15 | 360.2 | 191 |  | 1 |  | 71.8
2018-02-01 | 341.68 | 344.06 | 353.61 | 354.47 | 371.46 | 376.5 | 354.17 | 352.77 | 56.6 |  | 2 |  | 59.69
2018-03-01 | 347.68 | 341.12 | 348.67 | 355.16 | 373.7 | 375.76 | 353.4 | 360.34 | 100.8 |  | 3 |  | 46.34
2018-04-01 | 342 | 343.14 | 350.82 | 353.03 | 372.09 | 376.14 | 355.05 | 355.08 | 105.4 |  | 4 |  | 43.8
2018-05-01 | 340.58 | 343.55 | 355.82 | 360.12 | 373.6 | 374.55 | 356.54 | 353.32 | 43.2 |  | 5 |  | 30
2018-06-01 | 341.48 | 345.06 | 345.35 | 361.65 | 373.14 | 374.44 | 353.16 | 352.06 | 12.8 |  | 6 |  | 30
2018-07-01 | 341.46 | 344.5 | 358.25 | 359.29 | 373.06 | 376.89 | 354.17 | 356.65 | 71 |  | 7 |  | 50.76
2018-08-01 | 340.45 | 344.74 | 356.03 | 337.27 | 373.07 | 376.33 | 359.69 | 357.63 | 81 |  | 8 |  | 48
2018-09-01 | 343.25 | 346.63 | 353.82 | 359.46 | 372.08 | 376.36 | 354.26 | 357.7 | 127.4
2018-10-01 | 340.64 | 343.16 | 360.54 | 359.37 | 373.76 | 376.33 | 352.37 | 357.18 | 148
2018-11-01 | 340.65 | 344.71 | 360.62 | 359.24 | 372.94 | 376.28 | 354.7 | 357.9 | 169.4
2018-12-01 | 360.28 | 361.86 | 361.02 | 359.35 | 374.25 | 376.63 | 368.65 | 357.46 | 170.6
Between January - December 2018, all leachate wells on site have remained within the site compliance of 33m (for wells LW1, LW2, LW3, LW4, LW7 & LW8) and 5m (LW5 & LW6). Throughout 2018, the wells were serviced to ensure optimum leachate extraction, all of the leachate wells have now migrated from air pumps to electric pumps. The decision was taken that due to the nature of the leachate which was causing blockages that electric pumps are more efficient and less prone to breakdowns.
Treated Effluent
During this period 64,499m3 of treated leachate was released to the sewer.
The treated effluent is sampled and recorded monthly and tested for the following determinants:
pH / Suspended Solids / Ammoniacal Nitrogen / Temperature / Total Metals / Cyanide / Sulphide / Sulphate
The following results were recorded for the period:
Parameter 81703400 | pH | Suspended Solids | Ammoniacal Nitrogen | Temperature | Total Metals | Oil / Petroleum Spirit | Cyanide
Discharge Limit | 6-11 | 400 mg/l | 40 mg/l | 43oC | 2 mg/l | Nil | 1 mg/l
2018-01-01 | 7.6 | 136 | <0.41 | 17.2 | 0.698 | Nil | 0.047
2018-02-01 | 7 | 96 | <0.41 | 18.9 | 0.8135 | Nil | 0.043
2018-03-01 | 6.7 | 58 | 0.55 | 17.2 | 0.695 | Nil | 0.042
2018-04-01 | 7 | 136 | 0.53 | 22.2 | 0.9306 | Nil | 0.048
2018-05-01 | 7.4 | 154 | 26.2 | 16.2 | 1.0709 | Nil | 0.055
2018-06-01 | 7.4 | 28 | 8.73 | 15.6 | 0.9047 | Nil | 0.154
2018-07-01 | 7 | 80 | 1.27 | 18.9 | 0.7326 | Nil | 0.073
2018-08-01 | 7.1 | 360 | 13.3 | 14.9 | 0.8436 | Nil | 0.09
2018-09-01 | 5.9 | 34 | 11.2 | 14.2 | 0.8907 | Nil | 0.06
2018-10-01 | 7.1 | 15 | 0.65 | 18.1 | 0.7521 | Nil | 0.048
2018-11-01 | 7.1 | 60 | 12.3 | 22.2 | 0.9046 | Nil | 0.133
2018-12-01 | 7.4 | 80 | 0.61 | 18.4 | 0.8636 | Nil | 0.042
Parameter 81703400 | Sulphide | Sulphate |  | Whilst there are no compliance limits for pH under the permit RP3733PC, pH breached the Welsh Water discharge limit in September with a result of 5.9. All other parameters were compliant.
Discharge Limit | 2 mg/l | 1000 mg/l
2018-01-01 | 0.106 | 950
2018-02-01 | 0.126 | 334
2018-03-01 | 0.059 | 120
2018-04-01 | 0.032 | 95.7
2018-05-01 | <0.020 | 26.5
2018-06-01 | <0.020 | 19.4
2018-07-01 | 0.022 | 39.2
2018-08-01 | 0.049 | 121
2018-09-01 | <0.020 | 90.5
2018-10-01 | 0.028 | 157
2018-11-01 | <0.020 | 112
2018-12-01 | 0.043 | 132
3. Ground Water
Annual and Quarterly samples were recovered from groundwater boreholes: GW1, GW2, GW4, GW6, GW8, GW11, GW12 & GW13 during this period.
The most recent well to be added to the monitoring schedule was GW13 which was drilled in October 2012
The HRA was accepted by the Environment Agency in February 2013, and was reviewed in 2018 as part of the permit requirement to update the model every six years
The revised HRA was submitted to NRW in November 2018. The boreholes with compliance limits associated with them are GW1, GW2, GW9, GW10, GW11, and GW12
In addition the compliance limits have also been assessed for GW13 and were proposed in the 2014 annual report.
| 81701110 | 81701110 | 81701110 | 81701110 | 81701110 | 81701110 | 81701110
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 1.5 | 0.1 | 250 | 3 | 0.04 | 1 | 4
2018-02-06 | <0.41 | <0.07 | 11 | <1.0 | <0.04 | <0.02 | <1.0
2018-05-08 | <0.41 | <0.07 | 11.3 | <1.00 | <0.04 | 0.028 | <1.00
2018-09-12 | <0.41 | <0.07 | 8.2 | <1.00 | <0.04 | 0.013 | <1.00
2018-11-14 | <0.41 | <0.07 | 8.5 | <1.00 | <0.04 | <0.01 | <1.00
Unit | ug/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701120 | 81701120 | 81701120 | 81701120 | 81701120 | 81701120 | 81701120
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 17 | 0.16 | 650 | 15 | 1 | 1 | 65
2018-02-06 | 20.5 | <0.07 | 438 | <1.0 | 0.43 | 0.044 | 1.3
2018-05-10 | 18.5 | <0.07 | 344 | <1.00 | 0.45 | 0.106 | 1.93
2018-09-12 | 16.7 | 0.13 | 353 | <1.00 | 0.44 | 0.073 | <1.00
2018-11-14 | 17.5 | 1.06 | 423 | <1.00 | 0.39 | <2.0 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701130 | 81701130 | 81701130 | 81701130 | 81701130 | 81701130 | 81701130
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
Insufficient Sample
Insufficient Sample
Insufficient Sample
Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701140 | 81701140 | 81701140 | 81701140 | 81701140 | 81701140 | 81701140
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
2018-02-07 | 1.27 | <0.07 | 20.3 | <1.0 | <0.04 | <0.01 | <1.0
2018-05-14 | 1.12 | <0.07 | 17.4 | <1.00 | <0.04 | <0.02 | <1.00
2018-08-15 | 1.33 | <0.07 | 18.8 | <1.00 | <0.04 | <0.01 | <1.00
2018-11-30 | 1.27 | <0.07 | 31.9 | <1.00 | <0.04 | <1.00 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701150 | 81701150 | 81701150 | 81701150 | 81701150 | 81701150 | 81701150
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
2018-02-07 | Insufficient Sample
2018-05-14 | Insufficient Sample
2018-08-15 | Insufficient Sample
2018-11-30 | Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701160 | 81701160 | 81701160 | 81701160 | 81701160 | 81701160 | 81701160
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
2018-02-07 | 2.33 | <0.07 | 91.9 | <1.0 | 0.05 | 0.01 | <1.0
2018-05-14 | 3.1 | <0.07 | 66.5 | <1.00 | 0.06 | 0.022 | <1.00
2018-08-15 | 2.35 | <0.07 | 93.5 | <2.00 | <0.16 | <0.04 | <2.00
2018-11-30 | 2.52 | <0.07 | 130 | <1.00 | <0.08 | <1.00 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701170 | 81701170 | 81701170 | 81701170 | 81701170 | 81701170 | 81701170
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
2018-02-07 | Insufficient Sample
2018-05-14 | Insufficient Sample
2018-08-15 | Insufficient Sample
2018-11-30 | Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701180 | 81701180 | 81701180 | 81701180 | 81701180 | 81701180 | 81701180
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| NA | NA | NA | NA | NA | NA | NA
2018-02-07 | <0.41 | <0.07 | 74.3 | <1.0 | <0.08 | <0.01 | <1.0
2018-05-14 | <0.41 | <0.07 | 87.5 | <1.00 | <0.04 | 0.034 | <1.00
2018-08-15 | <0.41 | <0.07 | 91.5 | <2.00 | <0.04 | <0.01 | <2.00
2018-11-30 | <0.41 | <0.07 | 205 | <1.00 | <0.04 | <0.01 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701209 | 81701209 | 81701209 | 81701209 | 81701209 | 81701209 | 81701209
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 2.8 | 21 | 550 | 3 | 0.34 | 1 | 4
2018-02-07 | Insufficient Sample
2018-05-14 | Insufficient Sample
2018-08-15 | Insufficient Sample
2018-11-30 | Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701210 | 81701210 | 81701210 | 81701210 | 81701210 | 81701210 | 81701210
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 74 | 0.25 | 950 | 3 | 4.2 | 1 | 3
2018-02-07 | Insufficient Sample
2018-05-14 | Insufficient Sample
2018-08-15 | Insufficient Sample
2018-11-30 | Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701211 | 81701211 | 81701211 | 81701211 | 81701211 | 81701211 | 81701211
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
| 1.5 | 0.1 | 250 | 3 | 0.04 | 1 | 4
2018-02-07 | 1.27 | <0.07 | 43.5 | <1.0 | <0.04 | <0.02 | <1.0
2018-05-14 | Insufficient Sample
2018-08-15 | Insufficient Sample
2018-11-30 | Insufficient Sample
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701212 | 81701212 | 81701212 | 81701212 | 81701212 | 81701212 | 81701212
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 1.5 | 0.1 | 250 | 3 | 0.04 | 1 | 4
2018-02-06 | 5.41 | <0.07 | 99.5 | <1.0 | <0.04 | <0.02 | <1.0
2018-05-14 | 0.73 | 0.08 | 36.9 | <1.00 | <0.08 | 0.013 | <1.00
2018-08-15 | 0.94 | <0.07 | 50.9 | <2.00 | <0.04 | <0.01 | <2.00
2018-11-30 | 0.55 | <0.07 | 65.8 | <1.00 | <0.04 | <2.0 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
| 81701213 | 81701213 | 81701213 | 81701213 | 81701213 | 81701213 | 81701213
| Ammoniacal N | Cadmium | Chloride | Xylene | Mecoprop | Naphthalene | Toluene
limit | 1.5 | 0.1 | 250 | 3 | 0.07 | 1 | 4
2018-02-06 | 5.21 | <0.07 | 121 | <1.0 | <0.40 | <0.04 | <1.0
2018-05-08 | 0.45 | <0.07 | 68.2 | <1.00 | <0.04 | 0.061 | <1.0
2018-09-12 | <0.41 | <0.07 | 142 | <1.00 | <1.60 | <0.10 | <1.00
2018-11-14 | <0.41 | <0.07 | 89.2 | <1.00 | <0.08 | <0.10 | <1.00
Unit | mg/l | ug/l | mg/l | ug/l | ug/l | ug/1 | ug/l
Groundwater Trends 2018
2016-11-22
The above graphs show the Ammonia levels trends during the course of the year with a separate graph for GW12 & GW13.
From the above results, three groundwater boreholes exceeded the compliance limits for ammonia.
These were GW2 (06/02/18, 10/05/18, 14/11/18) GW 12 (06/02/18) & GW 13 (06/02/18)
GW2 saw a result of 20.5mg/l ammonia during February. This level reduced in May to 18.5mg/l & September to 16.7mg/l. This level then increased again during November to 17.5mg/l. The limit of Ammonia in this borehole is 17mg/l.
GW 2 exceeded the complaince limit for Cadmium on one occasion during November (14/11/18) with the limit at 0.16ug/l the results presented at level of 1.06ug/l.
GW 12 & 13 Boreholes had noticeably elevated levels of Ammonia during February. Analysis of GW12 recorded 5.41mg/l and GW13 5.21mg/l.
These boreholes have a limit of 1.5mg/l. The level was dramatically reduced with a downward trend during the remainder of this year as shown in the above graph
Ammonia levels in GW1, GW4 & GW8 showed a stable trend, in comparison to GW2, GW6, GW12 & 13 which showed more variable trends however these sample points have remained compliant.
Whilst most Chloride levels have demonstrated a stable trend, GW2 has seen a fall in concentration in May & August peaking once again in November. GW 13 shows variable trends throughout the year.
Mecoprop levels in GW 6 increased slightly during the first two quarters with a decrese during August and November.
Naphthalene shows a similar pattern during May with GW2, GW3, GW8, and GW12 showing a sudden increase, with all following a downward trend which continues into November.
The Cadmium levels in GW2 during February, May and September recorded relatively low levels, this peaked during Novembers quarterly sample.
To summarise some groundwater wells have experienced very low groundwater levels and slow recharge rates meaning that samples could not be taken from GW3, GW5, GW7, GW9, and GW10 throughout the period. We obtained a quarterly groundwater sample from GW11 during February but during May, August and November the level of groundwater had fallen. This could be associated with the location and extent of the material extraction at Miller Argent which is moving closer to the site boundary which may have had an effect on the groundwater levels around the site.
Trends from the above graph show that many of the groundwater boreholes including GW1, 2, 3, 4, 5, 8, 10, 11, 12 & 13 show minimal variation between January 2018 to December 2018. However GW6 saw a diffrence of 8 meters water level between January and July with this level steadily falling 5 meters towards December. GW 7 & 9 showed both variable trends throughout the year being quite inconsistant.
4. Landfill Gas
FID
| Parameter | FID
| 2018-01-01 | 12
| 2018-02-01 | 5
| 2018-03-01 | 38
| 2018-04-01 | 8
| 2018-05-01 | 40
| 2018-06-01 | 40
| 2018-07-01 | 10
| 2018-08-01 | 8
| 2018-09-01 | 20
| 2018-10-01 | 15
| 2018-11-01 | 30
| 2018-12-01 | 20
The site continues to pro-actively monitor surface emissions and the gas extraction system. Routine reviews of this data leads to the installation of temporary capping and gas infrastructure improvements to capture as much landfill gas as possible from the site. All complaints during this period were investigated with a FID Gastec around the site perimeter and supplemented with olfactory surveys at the receptors to identify the source of the odour. The reduction in odour complaints has continued from 2016 into 2018 recording 4 complaints.
External Borehole Monitoring
At present there are twenty-six external boreholes located on the outer perimeter of the site. All of these have been monitored during this period.
The following readings were recorded between January - December 2018
8171001 | CH4 | CO2 | 8171002 | CH4 | CO2 | 8171003 | CH4 | CO2 | 8171004 | CH4 | CO2
Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 3% V.V | 10% V.V
2018-01-01 | 0.5 | 2.4 | 2018-01-01 | 0.5 | 0.1 | 2018-01-01 | 0.6 | 3.3 | 2018-01-01 | 14.8 | 6.3
2018-02-01 | 0 | 1.9 | 2018-02-01 | 0 | 1.1 | 2018-02-01 | 0 | 1.8 | 2018-02-01 | 16.1 | 5.8
2018-03-01 | 0 | 1.4 | 2018-03-01 | 0 | 0.1 | 2018-03-01 | 0 | 4.4 | 2018-03-01 | 30.5 | 7.3
2018-04-01 | 0 | 1.9 | 2018-04-01 | 0 | 0.8 | 2018-04-01 | 0.1 | 5.3 | 2018-04-01 | 24.6 | 5.7
2018-05-01 | 0 | 1.2 | 2018-05-01 | 0 | 0.2 | 2018-05-01 | 0 | 0.8 | 2018-05-01 | 24.4 | 7.6
2018-06-01 | 0 | 0.7 | 2018-06-01 | 0 | 0.1 | 2018-06-01 | 0 | 0.3 | 2018-06-01 | 30.9 | 11.5
2018-07-01 | 0 | 0.5 | 2018-07-01 | 0 | 1.7 | 2018-07-01 | 0 | 0.1 | 2018-07-01 | 30.2 | 12.7
2018-08-01 | 0 | 0.8 | 2018-08-01 | 0 | 5.2 | 2018-08-01 | 0 | 0.3 | 2018-08-01 | 30.7 | 13.6
2018-09-01 | 0 | 1.4 | 2018-09-01 | 0 | 7 | 2018-09-01 | 0 | 1.3 | 2018-09-01 | 11 | 6.9
2018-10-01 | 0 | 1.7 | 2018-10-01 | 0 | 0.1 | 2018-10-01 | 0 | 1.6 | 2018-10-01 | 0 | 0.1
2018-11-01 | 0.1 | 1.3 | 2018-11-01 | 0 | 0.6 | 2018-11-01 | 0.1 | 1 | 2018-11-01 | 24.2 | 19.6
2018-12-01 | 0 | 1.7 | 2018-12-01 | 0 | 0.3 | 2018-12-01 | 0 | 4.5 | 2018-12-01 | 24.3 | 16
8171005 | CH4 | CO2 | 8171006 | CH4 | CO2 | 8171007 | CH4 | CO2 | 8171008 | CH4 | CO2
Permit Limit | 13% V.V | 17% V.V | Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 1% | 12%
2018-01-01 | 0.6 | 2.3 | 2018-01-01 | 0.5 | 7.5 | 2018-01-01 | 0.5 | 13.3 | 2018-01-01 | 1.7 | 13.3
2018-02-01 | 3 | 8.4 | 2018-02-01 | 0 | 7.7 | 2018-02-01 | 0 | 11.8 | 2018-02-01 | 3.6 | 13.5
2018-03-01 | 6.7 | 7.7 | 2018-03-01 | 0 | 7.7 | 2018-03-01 | 0 | 2.6 | 2018-03-01 | 0 | 11.2
2018-04-01 | 9.6 | 8.2 | 2018-04-01 | 0 | 7.6 | 2018-04-01 | 0 | 8.7 | 2018-04-01 | 0 | 11.5
2018-05-01 | 8.9 | 7.2 | 2018-05-01 | 0 | 5.6 | 2018-05-01 | 0 | 3.3 | 2018-05-01 | 0 | 0.9
2018-06-01 | 1.3 | 10.2 | 2018-06-01 | 0 | 4.9 | 2018-06-01 | 0 | 3.7 | 2018-06-01 | 0 | 2.9
2018-07-01 | 0.1 | 10.4 | 2018-07-01 | 0.1 | 3.3 | 2018-07-01 | 0.1 | 1.4 | 2018-07-01 | 0.1 | 1.5
2018-08-01 | 0 | 11.3 | 2018-08-01 | 0 | 3.4 | 2018-08-01 | 0 | 3.6 | 2018-08-01 | 0 | 3.1
2018-09-01 | 0 | 11.3 | 2018-09-01 | 0 | 3.8 | 2018-09-01 | 0 | 5.4 | 2018-09-01 | 0 | 3.2
2018-10-01 | 0 | 10.5 | 2018-10-01 | 0 | 4.4 | 2018-10-01 | 0 | 1.7 | 2018-10-01 | 0 | 2.7
2018-11-01 | 0.1 | 11.2 | 2018-11-01 | 0.1 | 5.8 | 2018-11-01 | 0 | 0.2 | 2018-11-01 | 0 | 7.3
2018-12-01 | 0 | 9.5 | 2018-12-01 | 0 | 6 | 2018-12-01 | 0.1 | 9.1 | 2018-12-01 | 0 | 7.7
8171009 | CH4 | CO2 | 8171010 | CH4 | CO2 | 8171011 | CH4 | CO2 | 8171012 | CH4 | CO2
Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 1% | 10%
2018-01-01 | 0.5 | 2.5 | 2018-01-01 | 0.5 | 1 | 2018-01-01 | 0.5 | 1.3 | 2018-01-01 | 0.6 | 0.9
2018-02-01 | 0 | 1.7 | 2018-02-01 | 0 | 2 | 2018-02-01 | 0 | 1.8 | 2018-02-01 | 0 | 1
2018-03-01 | 0 | 3.1 | 2018-03-01 | 0 | 2.3 | 2018-03-01 | 0 | 1 | 2018-03-01 | 0 | 0.9
2018-04-01 | 0 | 3 | 2018-04-01 | 0 | 2.1 | 2018-04-01 | 0 | 2 | 2018-04-01 | 0 | 1.1
2018-05-01 | 0 | 0.8 | 2018-05-01 | 0 | 0.6 | 2018-05-01 | 0 | 1.7 | 2018-05-01 | 0 | 0.6
2018-06-01 | 0 | 0.7 | 2018-06-01 | 0 | 0.1 | 2018-06-01 | 0 | 1.4 | 2018-06-01 | 0 | 0.5
2018-07-01 | 0.1 | 0.5 | 2018-07-01 | 0.1 | 0.1 | 2018-07-01 | 0.1 | 1.2 | 2018-07-01 | 0.1 | 0.5
2018-08-01 | 0 | 0.6 | 2018-08-01 | 0 | 0.4 | 2018-08-01 | 0 | 2.4 | 2018-08-01 | 0 | 0.8
2018-09-01 | 0 | 0.9 | 2018-09-01 | 0 | 0.1 | 2018-09-01 | 0 | 0.2 | 2018-09-01 | 0 | 1
2018-10-01 | 0 | 0.9 | 2018-10-01 | 0 | 1.1 | 2018-10-01 | 0 | 0.2 | 2018-10-01 | 0 | 0.8
2018-11-01 | 0 | 2 | 2018-11-01 | 0 | 2.4 | 2018-11-01 | 0 | 1.5 | 2018-11-01 | 0 | 0.6
2018-12-01 | 0.1 | 3.5 | 2018-12-01 | 0 | 0.3 | 2018-12-01 | 0 | 0.7 | 2018-12-01 | 0 | 0.6
8171013 | CH4 | CO2 | 81710014 | CH4 | CO2 | 8171015 | CH4 | CO2 | 8171016 | CH4 | CO2
Permit Limit | 1% | 10% | Permit Limit |  |  | Permit Limit | 1% | 16.7% | Permit Limit | N/A | 11.2
2018-01-01 | 0.6 | 5.7 | 2018-01-01 | 0.6 | 0.4 | 2018-01-01 | 0.6 | 9.8 | 2018-01-01 | 2.8 | 8.5
2018-02-01 | 0 | 5.3 | 2018-02-01 | 0 | 10.3 | 2018-02-01 | 0 | 10 | 2018-02-01 | 1.8 | 7.3
2018-03-01 | 0 | 4.5 | 2018-03-01 | 0 | 0.2 | 2018-03-01 | 0 | 9.7 | 2018-03-01 | 1.8 | 4.3
2018-04-01 | 0 | 4.8 | 2018-04-01 | 0 | 0.2 | 2018-04-01 | 0 | 10.5 | 2018-04-01 | 1.7 | 6.1
2018-05-01 | 0 | 2.9 | 2018-05-01 | 0 | 0.3 | 2018-05-01 | 0 | 7.9 | 2018-05-01 | 0 | 2.3
2018-06-01 | 0 | 4 | 2018-06-01 | 0 | 0.1 | 2018-06-01 | 0 | 5 | 2018-06-01 | 0 | 0.9
2018-07-01 | 0.1 | 3.8 | 2018-07-01 | 0.1 | 0.3 | 2018-07-01 | 0.1 | 2.6 | 2018-07-01 | 0.1 | 0.4
2018-08-01 | 0 | 3.8 | 2018-08-01 | 0 | 2.8 | 2018-08-01 | 0 | 6.9 | 2018-08-01 | 1 | 9.1
2018-09-01 | 0 | 3.5 | 2018-09-01 | 0.1 | 4.1 | 2018-09-01 | 0 | 8.6 | 2018-09-01 | 0.5 | 10.1
2018-10-01 | 0 | 0.7 | 2018-10-01 | 0.2 | 3.8 | 2018-10-01 | 0 | 7.6 | 2018-10-01 | 0 | 0.9
2018-11-01 | 0 | 3.2 | 2018-11-01 | 2.4 | 3 | 2018-11-01 | 0.1 | 8.3 | 2018-11-01 | 0.7 | 9.5
2018-12-01 | 0 | 3.7 | 2018-12-01 | 0.2 | 3.8 | 2018-12-01 | 0 | 8.4 | 2018-12-01 | 0.8 | 8.9
8171017 | CH4 | CO2 | 8171018 | CH4 | CO2 | 8171019 | CH4 | CO2 | 8171020 | CH4 | CO2
Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 1% | 10%
2018-01-01 | 0.5 | 2.3 | 2018-01-01 | 0.5 | 5 | 2018-01-01 | 0.5 | 8 | 2018-01-01 | 2 | 2.4
2018-02-01 | 0 | 2.7 | 2018-02-01 | 0 | 4 | 2018-02-01 | 0 | 7.8 | 2018-02-01 | 1.6 | 2.3
2018-03-01 | 0 | 1.4 | 2018-03-01 | 0 | 3.3 | 2018-03-01 | 0 | 8.2 | 2018-03-01 | 8.4 | 10.6
2018-04-01 | 0 | 1.7 | 2018-04-01 | 0 | 3.8 | 2018-04-01 | 0 | 8 | 2018-04-01 | 9.2 | 12.1
2018-05-01 | 0 | 0.2 | 2018-05-01 | 0 | 1.6 | 2018-05-01 | 0 | 5.8 | 2018-05-01 | 3.4 | 3.3
2018-06-01 | 0 | 0.4 | 2018-06-01 | 0 | 2.2 | 2018-06-01 | 0 | 2.9 | 2018-06-01 | 3.5 | 3.1
2018-07-01 | 0.1 | 0.2 | 2018-07-01 | 0.1 | 1.6 | 2018-07-01 | 0.1 | 1.2 | 2018-07-01 | 3.6 | 3.8
2018-08-01 | 0 | 0.3 | 2018-08-01 | 0 | 2.4 | 2018-08-01 | 0 | 1.9 | 2018-08-01 | 2.6 | 3.2
2018-09-01 | 0 | 0.3 | 2018-09-01 | 0 | 3.2 | 2018-09-01 | 0 | 2.8 | 2018-09-01 | 3 | 3
2018-10-01 | 0 | 0.3 | 2018-10-01 | 0 | 2.5 | 2018-10-01 | 0 | 3 | 2018-10-01 | 1.5 | 1.7
2018-11-01 | 0.1 | 3.1 | 2018-11-01 | 0.1 | 6.2 | 2018-11-01 | 0.1 | 5.5 | 2018-11-01 | 2.9 | 4.4
2018-12-01 | 0 | 0.1 | 2018-12-01 | 0 | 5.8 | 2018-12-01 | 0 | 5.4 | 2018-12-01 | 0 | 0.1
8171021 | CH4 | CO2 | 8171022 | CH4 | CO2 | 8171023 | CH4 | CO2 | 8171024 | CH4 | CO2
Permit Limit | 24.6% | 19.2 | Permit Limit | 1% | 10% | Permit Limit | 1% | 10% | Permit Limit | 29.7% | 9.7%
2018-01-01 | 28.8 | 24.8 | 2018-01-01 | 0.6 | 0.1 | 2018-01-01 | 0.6 | 2.1 | 2018-01-01 | 20.2 | 8.8
2018-02-01 | 25.4 | 21.5 | 2018-02-01 | 19 | 19.3 | 2018-02-01 | 0 | 4 | 2018-02-01 | 18.5 | 9
2018-03-01 | 26.7 | 21.1 | 2018-03-01 | 0 | 0.1 | 2018-03-01 | 0.4 | 2.4 | 2018-03-01 | 16.2 | 6.8
2018-04-01 | 25.4 | 21.5 | 2018-04-01 | 20 | 19.5 | 2018-04-01 | 0 | 1.6 | 2018-04-01 | 15.3 | 6.5
2018-05-01 | 24.5 | 21.8 | 2018-05-01 | 16.4 | 18.1 | 2018-05-01 | 0.1 | 4.9 | 2018-05-01 | 16 | 6.5
2018-06-01 | 22.9 | 22.2 | 2018-06-01 | 0 | 0.1 | 2018-06-01 | 0 | 3.5 | 2018-06-01 | 14.2 | 5.5
2018-07-01 | 20.5 | 24 | 2018-07-01 | 15.9 | 20 | 2018-07-01 | 0 | 1.9 | 2018-07-01 | 8.1 | 3.6
2018-08-01 | 20.5 | 23.9 | 2018-08-01 | 0 | 0.1 | 2018-08-01 | 0 | 1.9 | 2018-08-01 | 10 | 4.6
2018-09-01 | 21.2 | 20.2 | 2018-09-01 | 15.4 | 19 | 2018-09-01 | 0 | 2.7 | 2018-09-01 | 16.1 | 6.5
2018-10-01 | 22.8 | 22.3 | 2018-10-01 | 15.2 | 18.3 | 2018-10-01 | 0 | 3 | 2018-10-01 | 17.3 | 8.2
2018-11-01 | 23.8 | 23.2 | 2018-11-01 | 0 | 0.1 | 2018-11-01 | 0 | 4.2 | 2018-11-01 | 19.2 | 11.2
2018-12-01 | 16.6 | 14.7 | 2018-12-01 | 0.2 | 1.3 | 2018-12-01 | 0 | 2.6 | 2018-12-01 | 15.4 | 9.4
8171025 | CH4 | CO2 | 8171026 | CH4 | CO2
Permit Limit | 57.5% | 12.7 | Permit Limit | 37.9% | 15.9
2018-01-01 | 27.8 | 8.8 | 2018-01-01 | 20 | 15.9
2018-02-01 | 30.8 | 6.4 | 2018-02-01 | 9.7 | 16.3
2018-03-01 | 44.9 | 10 | 2018-03-01 | 2.4 | 7.5
2018-04-01 | 37.4 | 7.5 | 2018-04-01 | 5.1 | 13.9
2018-05-01 | 35.4 | 9.6 | 2018-05-01 | 8.4 | 16.3
2018-06-01 | 38.9 | 9.1 | 2018-06-01 | 0 | 11.2
2018-07-01 | 24.7 | 9 | 2018-07-01 | 0.3 | 12.2
2018-08-01 | 31.4 | 11.5 | 2018-08-01 | 1.6 | 12.4
2018-09-01 | 25.5 | 6.7 | 2018-09-01 | 7 | 10
2018-10-01 | 22.6 | 6.9 | 2018-10-01 | 16.3 | 10.6
2018-11-01 | 13.5 | 8.6 | 2018-11-01 | 7 | 10.2
2018-12-01 | 26.9 | 10.5 | 2018-12-01 | 1 | 14.4
An update to IC8 was submitted in January 2013 and a final version was agreed in April 2013 and compliance and action limits changed as identified in CAR form date 24/04/13
Compliance limits and action limits in the tables above have been transposed from CAR form 24/04/13.
As is well documented for the site there are old mine workings and current mine workings in the locality of the site which make the ground gas around the site complex. This coupled
with the old council run Merthyr Waste site adjacent to the current lined Biffa Site make the issue of gas migration in perimeter boreholes difficult to attribute to once specific source.
The gas extraction system is fully maintained, monitored and infrastructure added frequently to ensure the maximum flow off site through the engines and flares is maintained.
Below are graphs showing the methane and carbon dioxide percentages for the gas boreholes which exceeded compliance limits between January and December 2018, gas boreholes: GB4, GB5, GB7, GB8, GB20, GB21,GB22, GB23,
GB24, GB25 & GB26
Gas Compound
Site | LFG flared (M3) | LFG used in engines (M3) | Methane % | Total Electricity produced (MWh) |  | Electricity used internally(MWh)
Trecatti Total | 221620 | 17143395 | 47.9% | 25554 |  | 1354
5. Dust & Asbestos Monitoring
Dust monitoring is carried out in four locations and Asbestos at six locations every 6 months at the site.
Measurements are taken for total inhalable dust and Particulate matter <10 microns.
The results are collected over a 24 hour mean using a portable meter or equivalent.
Analysis was conducted in May and November for Deposited Dust Monitoring & PM10 by ALS and the results are as follows:
|  | D1 Filter | D2 Filter | D3 Filter | D4 Filter |  |  | D1 Filter | D2 Filter | D3 Filter | D4 Filter
PM10 Results | Date in | 2018-05-31 | 2018-05-31 | 2018-05-31 | 2018-05-31 |  | Date in | 2018-12-01 | 2018-12-01 | 2018-12-01 | 2018-12-01
| Date out | 2018-05-30 | 2018-05-30 | 2018-05-30 | 2018-05-30 |  | Date out | 2018-11-30 | 2018-11-30 | 2018-11-30 | 2018-11-30
| Time In | 10:37 | 10:00 | 10:10 | 10:20 |  | Time In | 10:27 | 9:55 | 10:11 | 10:18
| Time Out | 10:37 | 10:00 | 10:10 | 10:20 |  | Time Out | 10:55 | 10:28 | 10:35 | 10:44
| Pump Flow Rate (l/min) | 5 | 5 | 5 | 5 |  | Pump Flow Rate (l/min) | 5 | 5 | 5 | 5
| Sampling Period (min) | 1442 | 1442 | 1441 | 1441 |  | Sampling Period (min) | 1468 | 1473 | 1464 | 1466
| Initial Filter Weight (mg) | 125.1 | 124.38 | 127.92 | 129.61 |  | Initial Filter Weight (mg) | 125.78 | 135.46 | 136.7 | 137.62
| Final Filter Weight (mg) | 125.18 | 124.4 | 128.03 | 129.83 |  | Final Filter Weight (mg) | 126.09 | 135.53 | 136.86 | 134.82
| Net Weight Gain (Filt) (mg) | 0.08 | 0.02 | 0.11 | 0.22 |  | Net Weight Gain (Filt) (mg) | 0.31 | 0.07 | 0.16 | 2.8
| Particulate Matter <10 Microns (mg/m3) | 0.14 | 0.034 | 0.19 | 0.38 |  | Particulate Matter <10 Microns (mg/m3) | 0.042 | 0.01 | 0.02 | <0.0
|  | D1 Filter | D2 Filter | D3 Filter | D4 Filter |  |  | D1 Filter | D2 Filter | D3 Filter | D4 Filter
Deposited Dust | Date in | 2018-05-31 | 2018-05-31 | 2018-05-31 | 2018-05-31 |  | Date in | 2018-12-01 | 2018-12-01 | 2018-12-01 | 2018-12-01
Results | Date out | 2018-05-30 | 2018-05-30 | 2018-05-30 | 2018-05-30 |  | Date out | 2018-11-30 | 2018-11-30 | 2018-11-30 | 2018-11-30
| Time In | 10:37 | 10:00 | 10:10 | 10:20 |  | Time In | 10:29 | 9:53 | 10:10 | 10:17
| Time Out | 10:37 | 10:00 | 10:10 | 10:20 |  | Time Out | 10:57 | 10:21 | 10:37 | 10:48
| Volume of air sampled (m3) | 1.443 | 1.44 | 1.442 | 1.44 |  | Number of Days Exposed | 1 | 1 | 1 | 1
| Pump Flow Rate (l/min) | 1 | 1 | 1 | 1 |  | Mass of Undissolved Solids (mg) | 0.9 | 9.5 | 4.6 | 11.1
| Sampling Period (min) | 1443 | 1440 | 1442 | 1440 |  | Deposited Dust, Total Calc (mg/m2/day) | 22 | 230 | 110 | 270
| Initial Filter Weight (mg) | 1168.08 | 1170.63 | 1170.39 | 1173.25 |  | Frisbee Diameter (mm) | 230 | 230 | 230 | 230
| Final Filter Weight (mg) | 1168.27 | 1170.77 | 1170.5 | 1173.32
| Net Weight Gain (Filt) (mg) | 0.19 | 0.14 | 0.11 | 0.07
| Total Inhalable Dust for IOM (mg/m3) | 0.13 | 0.1 | 0.08 | 0.05
The results from ALS for Deposited Dust have been set out and worded differently from previous results during November's Monitoring.
There are 4 Monitoring locations for this Monitoring - D1, D2, D3 & D4
These results show increased levels of deposited dust at locations D2 & D4. The results for these two locations were queried with the lab and were found to be correct.
At the time of monitoring the wind direction was south westerly, average wind speed was 23 mph, max wind speed 40 mph. There was 5.6 mm of rainfall with heavy intermittant showers
ALS has since re-visited site to carry out monitoring of deposited dust monitoring . These results are presented below. The schedule notice has been updated.
The results show the deposited dust analysis is below the permit limit 200 mg/m3
| D1 Filter | D2 Filter | D3 Filter | D4 Filter
Date in | 2018-01-24 | 2018-01-24 | 2018-01-24 | 2018-01-24
Date out | 2018-01-23 | 2018-01-23 | 2018-01-23 | 2018-01-23
Time In | 11:40 | 11:20 | 11:25 | 11:30
Time Out | 11:40 | 11:21 | 11:26 | 11:31
Number of Days Exposed | 1 | 1 | 1 | 1
Mass of Undissolved Solids (mg) | 0.5 | 4 | 5.7 | 2.5
Deposited Dust, Total Calc (mg/m2/day) | 12 | 96 | 140 | 60
Frisbee Diameter (mm) | 230 | 230 | 230 | 230
Analysis was conducted in April and October for Asbestos Monitoring by Lucion and the results are as follows:
Asbestos Monitoring Results
2018-04-30
Sample | Start |  | End |  | Fibres (N) | Reported Result
| Time | Flow (l/min) | Time | Flow (l/min) |  | (f/ml)
D1 | 10:50 | 8 | 11:50 | 8 | 3.5 | <0.01
D2 | 9:29 | 8 | 10:29 | 8 | 3 | <0.01
D3 | 9:35 | 8 | 10:35 | 8 | 5 | <0.01
D4 | 9:37 | 8 | 10:37 | 8 | 6 | <0.01
D5 | 9:31 | 8 | 10:31 | 8 | 3 | <0.01
D6 | 10:51 | 8 | 11:51 | 8 | 4 | <0.01
2018-10-29
Sample | Start |  | End |  | Fibres (N) | Reported Result
| Time | Flow (l/min) | Time | Flow (l/min) |  | (f/ml)
D1 | 9:17 | 8 | 10:22 | 8 | 0 | <0.01
D2 | 9:04 | 8 | 10:10 | 8 | 0 | <0.01
D3 | 9:08 | 8 | 10:13 | 8 | 1 | <0.01
D4 | 9:13 | 8 | 10:16 | 8 | 0 | <0.01
D5 | 9:11 | 8 | 10:15 | 8 | 0 | <0.01
D6 | 9:19 | 8 | 10:25 | 8 | 1 | <0.01
6. Biogene
Biogene started operations in Trecatti during September 2018.
As stated in permit variation V0010, there are three Surface Water Monitoring Points that require analysis to comply with the requirements of this Permit.
Biogene send their samples of the required areas on a monthly basis to Chemtest for analysis and present their results of these samples.
Please find these results below.
SW Point 1 | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Oil/Grease
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
October | Insufficient flow |  |  |  | Non Visible
November | Insufficient flow |  |  |  | Non Visible
December | Insufficient flow |  |  |  | Non Visible
SW Point 2 | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Oil/Grease
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
October | 7.6 | 82 | 1 | 61 | Non Visible
November | 7.2 | 150 | 4.7 | 54 | Non Visible
December | 7.6 | 29 | 0.72 | 53 | Non Visible
SW Point 3 | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Oil/Grease
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
October | 8 | 90 | 3.5 | 19 | Non Visible
November | 8 | 59 | 3.7 | 36 | Non Visible
December | 6.7 | 42 | 4.1 | 110 | Non Visible
The suspended solid levels were elevated during November in surface water point 2.
The water was held in the Biogene lagoon to undergo settlement. As the results show, the levels of suspended solids at Surface Water 3 were below the permit levels during November and December.
The water is pumped to the site 385 Lagoon after receiving permission from a signed Biffa pump permit when the quality is compliant.

## Complaints
Year | No. of compliants
2000 | 244
2001 | 1082
2002 | 782
2003 | 422
2004 | 206
2005 | 191
2006 | 296
2007 | 702
2008 | 101
2009 | 25
2010 | 28
2011 | 65
2012 | 78
2013 | 22
2014 | 77
2015 | 62
2016 | 6
2017 | 5
2018 | 4

## Table S4.3
Table S4.3 Performance Parameters
Parameter | Frequency of assessment | Annual Total | Unit
Energy used including leachate treatment |  | 1363.68 | kWh

## Table S4.2
Table S4.2: Annual Production/treatment
Leachate | Cubic metres/year
Disposed of off site | 0
Disposed of onsite effluent treatment plant | 64499 | m3
recirculated into waste mass | no recirculation N/A
Surface water and/or groundwater | Cubic metres/year
Disposed of off site | 26148047 | m3
Disposed of to effluent treatment plant | 74564 | m3
landfill gas | Cubic metres/year
combustion in flares | 221620 | m3
combustion in gas engines | 17143395 | m3
other methods of gas utilisation | N/A