## ReadMe
Impingement & Entrainment data
suffix for year of survey
Entrainment_21 | count scaled to 106 m3 of water as in Table D-2 of Fish reports
Metadata_21 | CW flow, tide and weather notes over the 24 hour impingement survey, general comments
Total biomass_21 | Total mass (g) of fish impinged in 2021 by species
Total abundance_21 | Total number of fish impinged in 2021 by species
Note limited survey possible in 2020 due to Covid

## Entrainment_19
Common Name | 2019-04-16 | 2019-05-09 | 2019-05-30 | 2019-06-11 | 2019-06-25 | 2019-07-03 | 2019-07-17 | 2019-08-07
Goby family* | 6919 | 25595 | 122274 | 115412 | 245479 | 85852 | 57808 | 8753
Sand smelt | - | - | 1274 | 16404 | 19151 | 41682 | 2513 | -
Indeterminate* | - | 3656 | 3184 | 4687 | 4643 | 9954 | 4398 | 5002
Shanny | - | - | 1274 | 3515 | - | 3733 | - | -
Blenny family* | - | - | - | - | 2902 | 1244 | - | -
Two-spotted clingfish | 577 | 1219 | - | 586 | 1161 | - | - | -
Herring family* | 3460 | - | - | - | - | - | - | -
Corkwing wrasse | - | - | 637 | - | 580 | 1244 | 628 | -
Herring | 1153 | 1219 | - | - | - | - | - | -
Long-spined sea scorpion | - | - | 1911 | - | - | - | - | -
Snake pipefish | - | - | - | 586 | - | 622 | - | -
Painted goby | - | - | 637 | - | - | - | - | -
Greater pipefish | - | - | - | - | - | - | 628 | -
Solenette | - | - | - | - | - | 622 | - | -
Scorpionfish family* | - | - | - | - | - | 622 | - | -
Tompot blenny | - | - | - | 586 | - | - | - | -
Butterfly blenny | - | - | - | - | 580 | - | - | -
Common seasnail | 577 | - | - | - | - | - | - | -
EGGS* | 55352 | 81660 | 28021 | 5273 | 6964 | 1244 | 3142 | 625

## Metadata_19
Survey Date | Sample time | Net operatives | Sampling staff | Station flow | Spring/Neap | Max tidal Range (m) | Weather Obs | Comments
2019-01-14 | 08:00-08:00 | AS | HC & RG | 08:00-11:05 (33.1 m3s-1), 11:05-17:21 (30.6m3s-1), 17:21-00:01 (32.5m3s-1), 00:01-02:34 (16.34m3s-1), 02:34-03:13(20.8m3s-1), 03:13-04:10(24.4m3s-1), 4:10-5:11(28.8m3s-1), 5:11-5:35 (32.0m3s-1), 5:35-9:03 (39.09m3s-1) | Neap-1 | 3.3 | 09:15- Wind direction: SW, Cloud (%): 95, Rainfall (mm): 0, Temperature (day@09:15): 10°C
2019-01-15 | 08:00-08:00 | AS (signed by BW) | HC & RG | 08:00-21:00 (38m3/s), 21:00-21:30 (32m3/s), 21:30-22:00 (24m3/s), 22:00-23:30 (16m3/s), 23:30-04:00 (0m3/s), 04:00-06:30 (38m3/s), 06:30-08:00 (38m3/s). | Neap +0 | 3.1 | 08:00- Wind direction: SW, Cloud (%):100, Rainfall (mm): 0, Temperature (day@08:00): 10°C
2019-01-21 |  |  | HC & OMR | 08:00-09:47 (38.9m3/s) 09:47-12:58 (36.5m3/s), 12:58-16:31 (39.46m3/s), 16:31-01:07 (37:05m3/s) 01:07-03:52 (39.5m3/s), 03:52-08:50 (37.6m3/s) | Spring -2 | 6.8 | 09:15- Wind direction: W, Cloud (%): 100, Rainfall (mm): 0, Temperature (day@09:15): 7°C
2019-01-22 |  |  | HC & OMR | 08:00-13:22 (36.5m3/s), 13:22-16:36 (39.3m3/s), 16:36-20:33 (38.1m3/s), 20:33-01:54 (37.3m3/s), 01:54-04:44 (39.7m3/s) | Spring -1 | 7 | 12:00- Wind direction: NW, Cloud (%): N/A, Rainfall (mm): 0, Temperature (day @ 12:00): 7°C
2019-02-04 | 08:00-08:00 |  | WO & RG | 08:00-22:00 (38m3/s), 22:00-23:30 (30m3/s), 23:30-00:00 (15m3/s), 00:00-03:00 (0m3/s), 03:00-04:45 (10m3/s), 04:45-06:30 (step increase), 06:30-08:00 (38m3/s) | Spring -2 | 5.4 | 08:00- Wind direction: SW, Cloud (%): 50, Rainfall (mm): 0, Temperature (day @ 08:00) 8°C
2019-02-05 | 08:00-08:00 | BW & PD | WO & RG | 08:00-15:08 (37.1m3/s), 15:08-18:18 (39.4m3/s), 18:18-03:31 (37.0m3/s), 03:31-07:34 (39.1m3/s) | Spring -1 | 5.6 | 12:00 Wind direction: S, Cloud (%):N/A, Rainfall (mm): 0, Temperature (day @ 12:00) 7°C
2019-02-18 | 08:00-08:00 | AS | OMR & MA | 08:00-09:30 (15 m3/s), 09:30-11:00 (20 m3/s), 11:00-12:00 (34 m3/s), 12:00-14:30 (25 m3/s), 14:30-22:00 (38 m3/s), 22:00-00:00 (23 m3/s), 00:00-0300 (0 m3/s), 03:00-06:00 (STEPS 38 m3/s), 06:00-08:00 (38m3/s) | Spring -3 | 6.4 | 09:00 Wind direction: W, Cloud (50 %):N/A, Rainfall (mm): 0, Temperature (day @ 09:00) 11°C
2019-03-05 | 08:00-08:00 | AS | RG & WO | 08:00-22:30 (38 m3/s), 23:00-00:00 (step decrease), 00:00-04:30 (0 m3/s), 04:30 - 06:30 (step increase), 06:30-08:00 (38 m3/s). | Spring -3 | 5.5 | 09:00 wind direction: W, Cloud (%): 70, Rainfall (mm): 0, Temperature (day @ 09:00) 12°C
2019-03-25 | 08:00-08:00 |  | WO & OMR | 08:00-21:30 (30-35 m3/sec), 21:30-05:00 (7-8 m3/sec), then back upto 38 m3/sec | Spring +3 | 5.9 | 08:30 wind direction: NW, Cloud (%): 10, Rainfall (mm): 0, Temperature (day @ 08:30) 11°C, (night @ 20:30) 7°C
2019-03-26 | 08:00-08:00 |  | WO & OMR | 08:00-22:31 (38-39 m3/sec), 22:31-23:50 (33 m3/sec), 23:50-06:00 (16-17 m3/sec), 38-39 m3/sec thereafter. | Spring +4 | 4.9 | 08:30 wind direction: NE, Cloud (%): 10, Rainfall (mm): 0, Temperature (day @ 08:30) 11°C, (Night @ 20:30) 3°C
2019-04-09 | 08:15-08:15 | AS & PD | HC & RG | 08:15-08:15 (38-39 m3/sec) | Spring +2 | 5.6 | 08:30 wind direction: E, Cloud (%): 80, Rainfall (mm): 0 (light), Temperature (day @ 08:30) 12°C, (Night @ 20:30) 8°C
2019-04-14 | 09:00-09:00 | AS | MA & RG | 09:00-09:21 (23.7 m3/sec), 09:21-13:24 (25 m3/sec), 13:24-20:34 (23.5 m3/sec), 20:34-03:20 (25.3 m3/sec), 03:20-03:46 (27 m3/sec), 03:46-04:39 (33 m3/sec), 04:39-04:54 (33 m3/sec) | Neap +0 | 3.4 | 09:00 wind direction: SE, Cloud (%): 100, Rainfall (mm): yes, Temperature (day @ 09:00) 8°C
2019-04-15 | 09:00-09:00 | AS | HC & MA | 09:00-10:20 (30.9 m3/sec), 10:20-16:02 (33.9 m3/sec), 16:02-23:33 (31.4 m3/sec), 23:33-23:38 (24 m3/sec), 23:38-00:02 (8.5 m3/sec), 00:02-04:09 (13.6 m3/sec), 04:09-05:46 (26 m3/sec), 05:46-06:33 (33 m3/sec) | Neap +1 | 4.3 | 09:00 wind direction: E, Cloud (%): 100, Rainfall (mm): yes, Temperature (day @ 09:00) 8°C
2019-05-08 | 09:00-09:00 | AS | WO, OMR & PW | 08:30-11:13 (34.2m3/sec) 11:13-12:27 (34.5m3/sec), 12:27-23:40 (36.5m3/sec), 23:40-03:56 (23.91m3/sec), 03:56-04:10 (21.92m3/sec) 04:10-04:57 (26.4m3/sec), 04:57-05:19 (22.4m3/sec), 05:19-06:23 (30.9m3/sec), 06:23-06:51 (38.3m3/sec), 06:51-08:30 (38.9m3/sec) | Spring + 2 | 5.6 | 09:00 wind direction: S, Cloud (%): 100, Rainfall (mm): yes, Temperature (day @ 09:00) 9.5°C
2019-05-09 | 09:00-09:00 | AS | WO, OMR & PW | 8:30-19:25 (38.9m3/sec) 19:25-00:03 (25.5m3/sec), 00:03-04:19 (23.4m3/sec), 04:19-05:02 (28.07m3/sec), 05:02-06:00 (31.2m3/sec) 06:00-09:00 (33.3m3/sec) | Spring + 3 | 5.1 | 09:00 wind direction: SW, Cloud (%): 90, Rainfall (mm): no, Temperature (day @ 09:00) 13°C
2019-05-13 | 08:30-08:30 | AS & AM | RG & PW | 08:30-08:30 (31-33m3/sec) | Neap +0 | 3.7 | 08:30 wind direction: SE, Cloud (%): 15, Rainfall (mm): no, Temperature (day @ 08:30) 15°C, Temperature (night @ 20:30) 10°C
2019-05-28 | 08:30-08:30 | AS & AM | RG & AP | 08:30-08:30 (32-34m3/sec) | Neap +0 | 2.8 | 08:30 wind direction: NW, Cloud (%): 20, Rainfall (mm): no, Temperature (day @ 08:30) 15°C, Temperature (night @ 20:30) 12°C
43626 | 08:30-08:30 | AS & AM | HC & CF | 08:30-00:05 (30-34m3/sec), 00:05-06:30 (25m3/sec), 06:30-08:30 (32m3/sec) | Neap -1 | 4.2 | 08:30 wind direction: NE, Cloud (%): 30, Rainfall (mm): heavy at times, Temperature (day @ 08:30) 15°C, Temperature (night @ 20:30) 11°C | High number of mussels in trash due to wheel cleaning process
43627 | 08:30-08:30 | AS & AM | HC, CF & VG | 08:30-23:50 (31-34m3/sec), 23:50-4:20 (17m3/sec), 4:20-08:30 (31ms/sec) | Neap +0 | 4.1 | 08:30 wind direction: NE, Cloud (%): 100, Rainfall (mm): heavy at times, Temperature (day @ 08:30) 14°C, Temperature (night @ 20:30) 11°C | High number of mussels in trash due to wheel cleaning process
24-25/06/2019 | 08:00-08:00 | Enigma additional staff (unknown names) | OMR & HC | 06:40-11:00 (31m3/sec), 11:00-13:25 (33m3/sec), 13:25-16:26 (30m3/sec), 16:26-23:55 (34.5m3/sec), 23:55-00:05 (33.5m3/sec), 00:05-02:05 (17m3/sec), 02:05-04:05 (22m3/sec), 04:05-04:15 (16.5m3/sec), 04:15-5:30 (25m3/sec), 05:30 (31m3/sec) | Neap -3 | 3.4 | 09:00 wind direction: N, Cloud (%): 70, Rainfall (mm): N/A, Temperature (day @ 09:00) 15°C, Temperature (night) ?
25-26/06/2019 | 08:00-08:00 | Enigma additional staff (unknown names) | OMR & HC | 05:30-9:00 (31 m3/sec), 09:00-13:25 (32.5 m3/sec), 13:25-16:26 (30.5 m3/sec), 16:26-23:58 (34.5 m3/sec), 23:58-00:05 (33.4 m3/sec), 00:05-02:03 (17.5 m3/sec), 02:03-04:05 (20 m3/sec), 04:05-04:12 (16.5 m3/sec), 04:12-05:28 (25.5 m3/sec) | Neap -2 | 3 | 09:00 wind direction: NE, Cloud (0%): 70, Rainfall (mm): N/A, Temperature (day @ 09:00) 19°C, Temperature (night) ?
2-3/07/2019 | 08:00-08:00 | Enigma additional staff (unknown names) | OMR & RG | 09:00-13:10 (38m3/sec), 13:10-20:40 (37m3/sec), 20:40-01:00 (38.7m3/sec), 01:00-01:24 (37m3/sec), 01:24-01:45 (29.7m3/sec), 01:45-03:50 (36m3/sec), 03:50-08:00 (39.3m3/sec) | Spring -2 | 5.9 | 09:00 wind direction: S, Cloud (%): 0, Rainfall (mm): N/A, Temperature (day @ 09:00) 10°C, Temperature (night) ?
16-17/07/19 | 08:00-08:00 | AS & AM | HC & RG | 08:00-09:00 (23.5m3/sec), 09:00-13:25 (21.6m3/sec), 13:25-19:05 (24.5m3/sec), 19:05-19:30 (Max 28.46m3/sec), 19:30-19:58 (23.9m3/sec), 19:58-01:29 (min 21.3m3/sec), 01:29-07:31 (24.6m3/sec) | Spring -2 | 5.2 | 09:00 wind direction: SW, Cloud (%): 0, Rainfall (mm): N/A, Temperature (day @ 09:00) 19°C, Temperature (night) ?
17-18/07/19 | 08:00-08:00 | AS & AM | HC & RG | 08:00-09:00 (23.5m3/sec), 09:00-13:35 (21.5m3/sec), 13:35-19:53 (23.9m3/sec), 19:53-23:05 (22.7m3/sec), 23:05-23:12 (max 27.0m3/sec), 23:12-23:44 (22.2m3/sec), 23:44-01:58 (21.3m3/sec), 01:58-07:58 (23.8m3/sec) | Spring -1 | 5.4 | 09:00 wind direction: W, Cloud (%): 0, Rainfall (mm): N/A, Temperature (day @ 09:00) 18°C, Temperature (night) ?
05-06/08/19 | 08:00-08:00 | AS | HC RG CF | 08:00-10:21 (20.1m3/sec), 10:21-16:22 (33.2m3/sec), 16:22-22:26 (29.19m3/sec), 22:26-0:09 (33.6 m3/sec), 0:09-04:20 (7.59 m3/sec), 04:20-11:16 (7.12 m3/sec), 11:16-12:22 (32.8m3/sec) | Spring +2 | 6.3 | 12:00 wind direction: WSW, Cloud (%): 60, Rainfall (mm): 0, Temperature (day @ 12:00) 18°C, Temperature (night) n/a
06-07/08/19 | 08:00-08:00 | AS | RG CF | 08:00-11:15 (33.4m3/sec), 11:15-17:08 (29.6m3/sec),17:08-23:23 (32.7m3/sec), 23:23-03:39 (7.7 m3/sec), 03:39-04:00 (10.5m3/sec), 04:00-04:16 (12.4m3/sec), 04:16-04:34 (16.6m3/sec), 04:34-04:49 (20.7 m3/sec), 04:49-05:07 (16.4m3/sec), 05:07-05:45 (23.9 m3/sec), 05:45-06:45 (30.4 m3/sec), 06:45-08:00 (30.4 m3/sec) | Spring +3 | 5.6 | 12:00 wind direction: WSW, Cloud (%): 80, Rainfall (mm): 0, Temperature (day @ 12:00) 19°C, Temperature (night) n/a
27-28/08/19 | 08:00-08:00 | AS | HC CF | 06:33-10:30 (32.1m3/sec), 10:30-16:15 (30.8m3/sec), 16:15-08:04 (33.7m3/sec) | Neaps +2 | 4.3 | 12:00 wind direction: WSW, Cloud (%): 0, Rainfall (mm): 0, Temperature (day @ 12:00) 20°C, Temperature (night) n/a
28-29/08/19 | 08:00-08:00 | AS | HC CF | 08:04-11:40 (31.9m3/sec), 11:40-17:10 (30.4m3/sec), 17:10-18:17 (33.6m3/sec), 18:17-20:52 (33.7m3/sec),20:52-00:12 (29.7m3/sec), 00:12-03:21 (31.9m3/sec), 03:21-05:58 (31.9m3/sec), 05:58-07:59 33.5m3/sec), 07:59-08:00 (32.4 m3/sec) | Neaps +3 | 5.4 | 12:00 wind direction: WNW, Cloud (%): 30, Rainfall (mm): 0, Temperature (day @ 12:00) 14°C, Temperature (night) n/a
16-17/09/19 | 08:00-08:00 | AS | HC CF | 08:00 (16.6 m3/sec), 08:00-10:17 (15.7m3/sec), 10:17-10:24 (20.5 m3/sec), 10:24-11:09 (24.4m3/sec), 11:09-12:32 (22.4m3/sec), 12:32-13:45 (26.2 m3/sec), 13:45-16:32 (31.2 m3/sec), 16:32-20:00 (25.4m3/sec), 20:00-00:30 (22.9m3/sec), 00:30-04:36 (27.9m3/sec), 04:36-08:00 (33.9m3/sec) | Spring +0 | 5.8 | 08:30 wind direction: W/NW, Cloud (%): 5, Rainfall (mm): 0, Temperature (day @ 08:30) 17°C, Temperature (night): 15°C
17-18/09/19 | 08:00-08:00 | AS | HC CF | 08:00 (33.9m3/sec), 08:00-15.40 (30-35m3/sec), 15:40-23:40 (38m3/sec), 23:40-04:30 (0m3/sec), 04:30-08:00 (33m3/sec) | Spring +1 | 5.6 | 08:30 wind direction: NE, Cloud (%): 5, Rainfall (mm): 0, Temperature (day @ 08:30) 17°C, Temperature (night): 12°C
8-9/10/19 |  |  |  | 08:00-13:49 (31.5m3/sec), 13:49-17:22 (33.3m3/sec), 17:22-21:52 (32.1m3/sec), 21:52-22:46 (23.6m3/sec), 22:46-23:44 (15.9m3/sec), 23:44-00:02 (8.4m3/sec), 00:02-00:03 (0.0m3/sec), 00:03-4:04 (7.9m3/sec), 4:04-4:43 (16.2m3/sec), 4:43-05:35 (24.6m3/sec), 5:35-7:01 (31.8m3/sec). | Neap +2 | 2.9 | 12:00 wind direction: W, Cloud (%): 90, Rainfall (mm): 90, Temperature (day @ 12:00) 14°C
2019-10-09 |  |  |  |  | Neap +3 | 3.7
21-22/10/2019 | 08:30-08:30 | DW | HC WO | 08:30-16:00 (24-28m3/sec), 16:00-22:00 (31-33m3/sec), 22:00-01:00 (24m3/sec), 01:00-04:30 (15m3/sec), 04:30-08:30 (28m3/sec) | Neap -1 | 3.2 | 8:30 wind direction: E, Cloud (%): 20, Rainfall (mm): 0, Temperature (day @ 8:30) 13°C, (night @ 20:30) 11°C
18-19/11/19 | 08:30-08:30 | AS | OMR CF | 08:00-14:00 (38-39m3/sec), 14:00-17:00 (30-32m3/sec), 17:00-23:30 (38-39m3/sec), 23:30-02:00 (30-32m3/sec),23:30-08:00 (38-39m3/sec) | Neaps -2 | 4.2 | 12:00 wind direction: SE, Cloud (%): 99, Rainfall (mm): 0, Temperature (day @ 12:00) 11°C
25-26/11/2019 | 08:00-08:00 | AS | HC WO | 08:00 (38.4m3/sec), 08:00-11:10 (37.4m3/sec), 11.10-13:39 (39.3 m3/sec), 13:39-17:20 (38.6m3/sec), 17.20-20.05 (37.4m3/sec), 20.05-22.59 (36.9m3/sec), 22:59-00:57 (37.8m3/sec), 00:57-01:58 (38.7m3/sec), 01:58-03:21 (38m3/sec), 03:21-05:52 (38.3m3/sec), 05.52-08:00 (38.1m3/sec). | Spring -3 | 6.4 | 12:00 wind direction: S, Cloud (%): 99, Rainfall (mm): n/a, Temperature (day @ 12:00) 12°C
26-27/11/2019 | 08:00-08:00 | AS | HC WO | 08:00 (37.4m3/sec), 08:00-11:50 (37.4m3/sec), 11:50-14:54 (39m3/sec), 14:54-18:37 (38.2m3/sec), 18:37-21.42 (37.5m3/sec), 21:42-23:48 (37.3m3/sec), 23:48-00:06 (22.1m3/sec), 00:06-00:36 (21m3/sec), 00:36-03:02 (23.5m3/sec), 03:02-04:52 (24.8m3/sec), 04:52-05:17 (29.6m3/sec), 05:17-06:19 (32m3/sec), 06:19-08:00(32.9m3/sec) | Spring -2 | 6.5 | 08:30 wind direction: SW, Cloud (%): 20, Rainfall (mm): n/a, Temperature (day) 12°C, (night) 8°C
3-4/12/19 |  |  |  | 08:30-08:30 (37.5-39.5m3/sec) | Neap -2 | 3.2 | 08:30 wind direction: SW, Cloud (%): 20, Rainfall (mm): n/a, Temperature (day) 12°C, (night) 8°C
4-5/12/19 |  |  |  | 08:30-23:50 (37-39 m3/sec), 23:50-04:17 (31-33m3/sec), 04:14-05:23 (34-35m3/sec), 05:23-08:30 (38-39ms/sec) | Neap -1 | 2.8 | 08:30 wind direction: SW, Cloud (%): 80, Rainfall (mm): n/a, Temperature (day) 12°C, (night) 9°C
16-17/12/19 | 08:00-08:00 |  | HC MA | 08:00 (38.6 m3/sec), 08:00-12:20 (38.1 m3/sec), 12:20-14:20 (38.1 m3/sec), 14:20-17:03 (39.5m3/sec), 17:03-19:25 (38.4 m3/sec), 19:25-22:46 (38.2 m3/sec), 22:46-23:16 (32.37 m3/sec), 23:16-00:10 (15.8 m3/sec), 00:10-02:35 (14.4 m3/sec), 02:35-05:10 (15.7 m3/sec), 05:10-05:50 (25m3/sec), 05:50-06:33 (34.5 m3/sec), 06:33-07:20 (38.5 m3/sec), 07:20-08:00 (38.9 m3/sec) | Spring +2 | 5.4 | 12:00 wind direction: SW, Cloud (%): 80, Rainfall (mm): n/a, Temperature (day @ 12:00) 6°C
17-18/12/19 | 08:00-08:00 |  | HC MA | 08:00 (38.9 m3/sec), 08:00-12:05 (38.3 m3/sec), 12:05-15:45 (38.4 m3/sec), 15:45-17:45 (39.6 m3/sec), 17:45-20:45 (38.1 m3/sec), 20:45-23:15 (38.2 m3/sec), 23:15-00:30 (38.4 m3/sec), 00.30-01:00 (38.8 m3/sec), 01:00-03:25 (38.1 m3/sec), 03:25-04:45 (38.3 m3/sec), 04:45-06:00 (39 m/sec), 06:00-08:00 (38.9 m3/sec) | Spring +3 | 5 | 12:00 wind direction: WSW, Cloud (%): 90, Rainfall (mm): n/a, Temperature (day @ 12:00) 9°C
Note on G1: Young, Hannah: Maximum consequtive tidal range during survey period.
Note on E12: Cooper, Harry: [apart from 23:00-05:00 (8th to 9th) at 8m3/sec] this is outside sampling window so didn’t add
Note on E28: Cooper, Harry: mixed with 2nd days metadata
Note on H40: Oliver, Will: Rainfall listed as 50%
Note on H41: Oliver, Will: Rainfall listed as 50%

## Total Biomass_19
MAIN CATCH BIOMASS + TRASH BIOMASS
Species | 2019-01-14 | 2019-01-15 | 2019-01-21 | 2019-01-22 | 2019-02-04 | 2019-02-05 | 2019-02-18 | 2019-03-05 | 2019-03-25 | 2019-03-26 | 2019-04-09 | 2019-04-15 | 2019-04-16 | 2019-05-07 | 2019-05-08 | 2019-05-13 | 2019-05-27 | 2019-06-10 | 2019-06-11 | 2019-06-24 | 2019-06-25 | 2019-07-03 | 2019-07-16 | 2019-07-17 | 2019-08-05 | 2019-08-06 | 2019-08-27 | 2019-08-28 | 2019-09-16 | 2019-09-17 | 2019-10-08 | 2019-10-09 | 2019-10-21 | 2019-11-18 | 2019-11-25 | 2019-11-26 | 2019-12-03 | 2019-12-04 | 2019-12-16 | 2019-12-17
Pogge | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11 | 20 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 15 | 35 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 49 | 0 | 32 | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 105 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 14 | 5 | 2055 | 6425 | 432 | 325 | 16 | 1050 | 447 | 526 | 131 | 309 | 38 | 4 | 14 | 0 | 2 | 0 | 0 | 5 | 6 | 0 | 0 | 0 | 2 | 2 | 1 | 1 | 1 | 19 | 291 | 59 | 22 | 74 | 210 | 868 | 196 | 110 | 24347 | 7251
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 0 | 17 | 0 | 4 | 0 | 5 | 13 | 0 | 0 | 9 | 9 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 0 | 0 | 0 | 12
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 131 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 10 | 5 | 17 | 6 | 8 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 0 | 0 | 235 | 11 | 17 | 14 | 0 | 24 | 11
Herring | 0 | 0 | 98 | 258 | 8 | 27 | 0 | 0 | 0 | 0 | 0 | 0 | 17 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 24 | 0 | 113 | 108 | 22
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 44 | 26 | 172 | 486 | 62 | 16 | 8 | 32 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 287 | 99 | 223 | 168 | 32 | 3258 | 3394
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 0 | 0 | 0 | 53 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 14 | 0
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 0 | 0 | 100 | 217 | 0 | 0 | 0 | 6 | 7 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 57 | 0 | 40 | 40 | 37 | 26 | 209 | 152
Bib | 145 | 0 | 55 | 492 | 25 | 97 | 0 | 0 | 0 | 155 | 0 | 215 | 107 | 155 | 402 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 63 | 0 | 24 | 30
Cod | 0 | 0 | 103 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 0 | 0 | 480 | 121 | 0 | 0 | 0 | 77 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 85 | 0 | 0 | 0 | 14 | 16
Poor cod | 29 | 8 | 139 | 675 | 100 | 35 | 13 | 93 | 18 | 64 | 47 | 0 | 0 | 1 | 0 | 0 | 29 | 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 71 | 29
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 139 | 277 | 145 | 43 | 0 | 0 | 29 | 0 | 105 | 0 | 17 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 0 | 14 | 13 | 8 | 0 | 0 | 31 | 28 | 46 | 78 | 58 | 84 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 16 | 6 | 0 | 9 | 7 | 24 | 8
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0
Black goby | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 24
Common goby | 0 | 1 | 1 | 5 | 4 | 2 | 1 | 0 | 2 | 6 | 1 | 1 | 1 | 5 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 3 | 1 | 0 | 1 | 0 | 1
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Painted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 9 | 2
Rock goby | 0 | 0 | 1 | 10 | 24 | 13 | 1 | 2 | 1 | 1 | 0 | 3 | 13 | 11 | 1 | 1 | 3 | 20 | 0 | 2 | 1 | 16 | 9 | 3 | 7 | 16 | 28 | 0 | 28 | 49 | 32 | 31 | 9 | 10 | 13 | 17 | 0 | 0 | 18 | 5
Sand goby | 1 | 5 | 58 | 171 | 25 | 8 | 43 | 92 | 4 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 12 | 10 | 12 | 1 | 0 | 939 | 330
Transparent goby | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 6 | 6 | 2 | 1 | 1 | 0
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 52 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 16 | 25
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Bass | 0 | 0 | 110 | 63 | 0 | 125 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 237 | 0 | 0 | 0 | 0 | 0 | 135 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 81 | 104 | 209 | 171 | 37 | 192 | 77
Striped red mullet | 0 | 0 | 0 | 22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 0 | 0 | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 23 | 52 | 68 | 0 | 0 | 51 | 15
Mullet indet | 0 | 0 | 0 | 1 | 1 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 1 | 0 | 0 | 1 | 0
Thin lipped grey mullet | 0 | 0 | 0 | 115 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 87 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 6 | 4
Dab | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 66 | 0 | 0 | 0 | 65
Flounder | 32 | 353 | 0 | 190 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plaice | 136 | 79 | 117 | 64 | 0 | 0 | 0 | 0 | 81 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 380 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 522 | 287 | 2747 | 10865 | 726 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 717 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 490 | 0 | 0 | 0 | 0 | 1379 | 1417
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 44 | 38 | 0 | 20 | 16 | 30 | 31 | 29 | 29 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 8 | 4 | 6 | 0 | 10 | 32
Nilsson's pipefish | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 2 | 5 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 2 | 0 | 10 | 9
Worm pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 23 | 65 | 352 | 80 | 0 | 0 | 54 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 45 | 10 | 0 | 0 | 77 | 51
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 40 | 0 | 0 | 0 | 100 | 26 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 31 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 44 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 0

## Total Abundance_19
MAIN CATCH ABUNDANCE + TRASH ABUNDANCE
Species | 2019-01-14 | 2019-01-15 | 2019-01-21 | 2019-01-22 | 2019-02-04 | 2019-02-05 | 2019-02-18 | 2019-03-05 | 2019-03-25 | 2019-03-26 | 2019-04-09 | 2019-04-15 | 2019-04-16 | 2019-05-07 | 2019-05-08 | 2019-05-13 | 2019-05-27 | 2019-06-10 | 2019-06-11 | 2019-06-24 | 2019-06-25 | 2019-07-03 | 2019-07-16 | 2019-07-17 | 2019-08-05 | 2019-08-06 | 2019-08-27 | 2019-08-28 | 2019-09-16 | 2019-09-17 | 2019-10-08 | 2019-10-09 | 2019-10-21 | 2019-11-18 | 2019-11-25 | 2019-11-26 | 2019-12-03 | 2019-12-04 | 2019-12-16 | 2019-12-17
Pogge | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 2 | 2 | 337 | 1262 | 46 | 30 | 3 | 228 | 48 | 47 | 8 | 30 | 4 | 2 | 2 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 | 3 | 1 | 2 | 1 | 19 | 183 | 51 | 6 | 17 | 67 | 165 | 20 | 11 | 2584 | 634
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 1
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 12 | 6 | 18 | 7 | 4 | 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 0 | 0 | 203 | 14 | 23 | 18 | 0 | 14 | 10
Herring | 0 | 0 | 21 | 60 | 2 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 6 | 0 | 1 | 18 | 6
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 56 | 33 | 182 | 490 | 62 | 26 | 10 | 36 | 4 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 282 | 114 | 210 | 167 | 30 | 2950 | 2786
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 0 | 0 | 1 | 3 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 1 | 1 | 1 | 1 | 7 | 3
Bib | 1 | 0 | 1 | 8 | 1 | 2 | 0 | 0 | 0 | 2 | 0 | 2 | 1 | 2 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Cod | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 0 | 0 | 5 | 4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
Poor cod | 4 | 2 | 14 | 52 | 7 | 3 | 1 | 7 | 1 | 5 | 2 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 2 | 2
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 1 | 2 | 3 | 1 | 0 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 0 | 3 | 2 | 1 | 0 | 0 | 3 | 4 | 4 | 6 | 5 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 4 | 1 | 0 | 2 | 1 | 7 | 4
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
Black goby | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 4
Common goby | 0 | 1 | 1 | 5 | 5 | 2 | 1 | 0 | 4 | 9 | 2 | 1 | 1 | 6 | 4 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 3 | 7 | 4 | 0 | 1 | 0 | 1
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Painted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 10 | 2
Rock goby | 0 | 0 | 1 | 7 | 3 | 2 | 1 | 2 | 1 | 3 | 0 | 1 | 4 | 4 | 1 | 1 | 1 | 7 | 0 | 1 | 1 | 5 | 2 | 1 | 2 | 5 | 4 | 0 | 5 | 11 | 5 | 7 | 5 | 3 | 12 | 4 | 0 | 0 | 5 | 4
Sand goby | 1 | 1 | 22 | 62 | 9 | 4 | 16 | 40 | 2 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 8 | 5 | 8 | 1 | 0 | 438 | 135
Transparent goby | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 29 | 16 | 5 | 1 | 2 | 0
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 6 | 6
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Bass | 0 | 0 | 2 | 4 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 13 | 27 | 13 | 5 | 28 | 12
Striped red mullet | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 0 | 0 | 2 | 1
Mullet indet | 0 | 0 | 0 | 4 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 3 | 0 | 0 | 1 | 0
Thin lipped grey mullet | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Dab | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
Flounder | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plaice | 2 | 1 | 2 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 1 | 1 | 5 | 18 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 5 | 2
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 2 | 0 | 1 | 1 | 2 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 6 | 4 | 1 | 0 | 1 | 3
Nilsson's pipefish | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 1 | 2 | 3 | 2 | 1 | 1 | 2 | 1 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 2 | 0 | 3 | 2
Worm pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 1 | 2 | 10 | 3 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 4 | 2
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 2 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0

## Entrainment_20
Common Name | 2020-07-14 | 2020-07-28 | 2020-09-02
Goby family* | 91976 | 13348 | 161777
Indeterminate* | 0 | 0 | 8185
Sand smelt | 1780 | 0 | 2889
Corkwing wrasse | 3560 | 607 | 0
Nilsson’s pipefish | 0 | 607 | 0
Straight-nose pipefish | 0 | 607 | 0
Two-spotted clingfish | 593 | 0 | 0
Sea scorpion family* | 593 | 0 | 0
EGGS* | - | - | -
Note reduced survey because of covid

## Metadata_20
Survey Date | Sample time | Net operatives | Sampling staff | Station flow (m3/Sec) | Spring/Neap | Max tidal Range (m) | Weather Obs | Comments
13-14/01/2020 | 08:00-08:00 | AM+ AS | HC + WO | 08:00-11:40 (37.9), 11:40-13:30 (37.9), 13:30-17:36 (38.2), 17:36-19:50 (38.9), 19:50-20:30 (38.8), 20:30-21:50 (25.6), 21:50-23:50 (16.6), 23:50-00:00 (8.2), 00:00-02:45 (8.1), 02:45-04:02 (7.4), 04:02-04:45 (12.1), 04:45-05:15 (25.4), 05:15-06:05 (29), 06:05-08:00 (33.5), 08:00 (38.4) | Spring +0 | 6.4 | 12:00 - Wind direction: S, Cloud (%): 100, Rainfall (mm): 100%, Temperature (day @ 12:00) 10°C, Storm Brendan-strong gusts, heavy rain
15-16/01/2020 | 08:00-08:00 | AM + AS | HC + WO | 08:00-11:30 (38.3), 11:30-14:00 (37.6), 14:00-17:32 (37.8), 17:32-20:20 (38.8), 20:20-20:40 (38.1), 20:40-22:00 (33.7), 22:00-23:30 (16.9), 23:30-00:00 (8.3), 00:00-02:12 (8.1), 02:12-02:45 (7.6), 02:45-04:02 (12.1), 04:02-05:05 (15.8), 05:05-06:05 (20.5), 06:05-08:00 (25.1), 08:00 (33.4) | Spring+1 | 6.3 | 12:00 - Wind direction: SW, Cloud (%): 100, Rainfall (mm): 90%, Temperature (day @ 12:00) 11°C, Storm Brendan-gusts, some sunny spells, rain
27-28/01/2020 |  |  |  | 08:00-12:00 (37.8), 12:00-16:30 (38.4), 16:30-20:00 (39.5), 20:00-23:53 (38.5), 23:53-00:30 (38.6), 00:30-02:40 (31.40), 02:40-04:20 (22.3), 04:20-04.40 (23.58), 04.40-05:00 (28.1), 05:00-05:50 (32.5), 05:50-08:00 (35.1), 08:00 (38.8) | Spring+1 | 5.7 | 12:00- Wind direction WSW, Cloud (%): 90, Rainfall (mm): 90%, Temperature (day @ 12:00) 9°C
11-12/02/2020 | 08:00-08:00 | AM + AS | HC + WO | 08:36-12:00 (34.91), 12:00-14:00 (31.2), 14:00-17:30 (29.9), 17:30-20:00 (32.6), 20:00-23:35 (34.5), 23:35-04:40 (0.0), 04:40-05:30 (4.0), 05:30-6:20 (8.6), 6:20-08:00 (20.4), 08:00 (25.6) | Spring +0 | 7.2 | 12:00- Wind direction W, Cloud (%): 90, Rainfall (mm): 100, Temperature (day @ 12:00) 5°C
12-13/02/2020 | 08:00-08:00 | AM + AS | HC + WO | 08:00-10:49 (25.6), 10:49-11:16 (24.6), 11:16-14:19 (16.1), 14:19-15:09 (14.5), 15:09-15:46 (19.1), 15:46-16:36 (22.3), 16:36-18:56 (27.9), 18:56-20:24 (33.8), 20:24-22:51 9 (34.9), 22:51-23:30 (33.3), 23:30-00:14 (15.9), 00:14-04:59 (0.00), 04:59-05:24(0.10), 05:24-05:42 (12.8), 05:42-06:21 (17.6), 06:21-07:59 (25.1), 07:59 (34.1) | Spring +1 | 7.1 | 12:00- Wind direction WNW, Cloud (%): 90, Rainfall (mm): 50, Temperature (day @ 12:00) 8°C | Ongoing work on drumscreen 3. All drumscreens were moving other than 3
17-18/02/2020 | 08:00-08:00 | AM + AS | OMR +TE | 08:00-09:31 (24.1), 09:31-10:30 (24.5), 10:30-12:13 (29.2), 12:13-14:37 (25.2), 14:37-21:54 (34.0), 21:54-22:35 (33.2), 22:35-23:34 (24.8), 23:34-00:00 (16.6), 00:00-00:20 (8.3), 00:20-03:30 (0.00), 03:30-04:27 (4.2), 04:27-05:06 (7.7), 05:06-05:40 (16.9), 05:40-06:10 (21.3), 06:10-06:21 (24.7), 06:21-07:59 (28.5), 07:59 (31.8) | Neap -1 | 3.2 | 12:00- Wind direction W, Cloud (%): 50 Rainfall (mm): 50, Temperature (day @ 12:00) 10°C | Drumscreen 3 work ongoing
18-19/02/2020 | 08:00-08:00 | AM + AS | OMR +TE | 08:00-11:40 (32.1), 11:40-12:06 (32.9), 12:06-14:25 (24.7), 14:25-14:57 (24.8), 14:57-15:22 (29.2), 15:22-19:23 (33.3), 19:23-19:53 (32.1), 19:53-23:19 (35.5), 23:19-00:08 (15.8), 03:53-04:28 (16.4), 04:28-05:01 (20.6), 05:01-05:41 (29.5), 05:41-07:59 (33.0), 07:59 (38.6) | Neap +0 | 3 | 12:00- Wind direction WSW, Cloud (%): 70 Rainfall (mm): 90, Temperature (day @ 12:00) 10°C | Ongoing work on drumscreen 3.
2-3/03/2020 | 08:00-08:00 | AM + AS | HC WO | 08:00-09:20 (38.4), 09:20-13:30 (37.9), 13:30-13:45 (38.2), 13:45-14:15 (32.4), 14:15-14:50 (34.9),14:15-15:10 (34.8), 15:10-19:55 (38.8), 19:55-00:00 (39.3), 00:00-03:55 (24.5), 03:55-04:30 (23.3), 04:30-05:20 (32.2), 05:20-05:40 (34.7), 05:40-08:00 (38.5), 08:00 (38.4) | Neap -2 | 3.3 | 12:00- Wind direction WNW, Cloud (%): 50 Rainfall (mm): 0, Temperature (day @ 12:00) 8°C
3-4/03/2020 | 08:00-08:00 | AM + AS | HC WO | No flows-metadata sheet no longer asks for flow | Neap -1 | 2.5 | 12:00- Wind direction WNW, Cloud (%): 70 Rainfall (mm): 50, Temperature (day @ 12:00) 9°C
16-17/03/2020 | 08:00-08:00 | AM + AS | HC TE | 08:00-13:00 (32-35), 13:00-08:00 (38-39) | Neap -2 | 3.7 | 08:30- Wind direction E, Cloud (%): 10, Rainfall (mm): 0, Temperature (day @ 08:30) 5°C, (Night), 2°C
2020-06-02 | 8hrs | AM + AS | HC OMR |  | Neap +2 | 4.8
2020-06-03 | 8hrs | AM + AS | HC OMR |  | Neap +3 | 5.5
2020-06-04 | 8hrs | AM + AS | HC OMR |  | Spring -3 | 6.1
2020-06-22 | 8hrs | AM + AS | HC OMR |  | Spring -1 | 5.5
2020-06-23 | 8hrs | AM + AS | HC OMR |  | Spring +0 | 5.5
2020-06-24 | 8hrs | AM + AS | HC OMR |  | Spring +1 | 5.5
13-14/07/2020 | 08:00-08:00 | AM + AS | HC OMR | No maintenance undertake. 4/7-6/7 flow low, 0-15 m3/s, 6/7-13/7 flow variable from 22-38 m3/s average 32 m3/s | Neap - 1 | 3.1 | 08:00- Wind speed (mph) 15, Wind direction W, Cloud (%): 100, Rainfall (mm): Yes steady rainfall heavy at times, Temperature (day @ 08:00) 15°C
14-15/07/2020 | 08:00-08:00 | AM + AS | HC OMR |  | Neap +0 | 2.9
27-28/07/20 | 08:00-08:00 | AM + AS | HC OMR | Low running over weekend (prior 2 days), ranging from 8 (overnight) to 22 (during the day) m3/s. | Neap -2 | 4.7 | 08:00- Wind speed (mph) 30, Wind direction SSW, Cloud (%): 100, Rainfall (mm): heavy, Temperature (day @ 08:00) 16°C
28-29/07/20 | 08:00-08:00 | AM + AS | HC OMR | Steady abstraction for the 3 days leading up to that at 29-33 m3/s. Nothing else exceptional. | Neap -1 | 4 | 08:00- Wind speed (mph) 30, Wind direction SSW, Cloud (%): 100, Rainfall (mm): heavy, Temperature (day @ 08:00) 16°C
3-4/08/20 | 08:00-08:00 | AM + AS | HC OMR | MCW flow consistent for the full week leading into the survey ranging from 30 - 33 m3/s. During the survey (03 - 06 August) it dropped to 23m3/s for 24hrs before rising again to 30 - 33 m3/s and then falling to 8 m3/s for the final day of the survey. | Spring -2 | 5.5 | 18:00- Wind speed (mph) 10, Wind direction NW, Cloud (%): no info, Rainfall (mm): minimal, light overnight probably, Temperature (day @ 08:00)15°C-17°C throughout
4-5/08/20 | 08:00-08:00 | AM + AS | HC OMR | MCW flow consistent for the full week leading into the survey ranging from 30 - 33 m3/s. During the survey (03 - 06 August) it dropped to 23m3/s for 24hrs before rising again to 30 - 33 m3/s and then falling to 8 m3/s for the final day of the survey. | Spring -1 | 5.8 | 06:00- Wind speed (mph) 25, Wind direction S, Cloud (%): no info, Rainfall (mm): minimal, light overnight probably, Temperature (day @ 08:00)15°C-17°C throughout
5-6/08/20 | 08:00-08:00 | AM + AS | HC OMR | MCW flow consistent for the full week leading into the survey ranging from 30 - 33 m3/s. During the survey (03 - 06 August) it dropped to 23m3/s for 24hrs before rising again to 30 - 33 m3/s and then falling to 8 m3/s for the final day of the survey. | Spring +0 | 5.8 | 06:00- Wind speed (mph) 4, Wind direction SSE, Cloud (%): no info, Rainfall (mm): minimal, light overnight probably, Temperature (day @ 08:00)15°C-17°C throughout
2-3/09/20 | 08:00-08:00 | AM+AS | HC TE OMR |  | Spring -1 | 5.8
14-15/09/2020 | 08:00-08:00 | AM+AS | HC OMR |  | Neap +2 | 4.3
6-7/10/20 | 08:00-08:00 | AM+AS | HC AW | 08:00-22:00 (37), 22:00-00:00 (37-8), 00:00-04:00 (8), 04:00-07:00 (8-38), 07:00-08:00 (38) | Spring +3 | 5.4 | Eel grass/ mussels in fish retention tank impeding valve operation. Works to remove most of the eel grass/mussel completed.
7-8/10/20 | 08:00-08:00 | AM+AS | HC AW | 08:00-22:00 (37), 22:00-00:00 (37-8), 00:00-04:00 (8), 04:00-05:00 step increase (to 12), 05:00-07:00 (12-38), 07:00-08:00 (38) | Spring +4 | 4.2 | 12:00 - wind speed (mph) 11, wind direction SW, Eel grass/ mussels in fish retention tank impeding valve operation. Works to remove most of the eel grass/mussel completed.
12-13/10/20 | 08:00-08:00 | AM+AS | HC AW | 08:00-09:30 (31), 09:30-10:00 (34), 10:00-14:00 (31.5-32), 14:00-21:00 (32-30.5), 21:00-03:00 (30.5-32), 03:00-04:00 (33.5), 04:00-08:00 (37) | Neap +1 | 3.4 | 08:00 - wind speed (mhp) 19.5 (drops to 14 at 18:00 to 30 at 08:00), Wind direction S, Temperature (Day @ 08:00) 13-11°C, (night @ 20:00) 12-11°C
13-14/10/20 | 08:00-08:00 | AM+AS | HC AW | 08:00-12:00 (37-38), 12:00-22:00 (38-37), 22:00-01:00 (37-38), 01:00-08:00 (38-37) | Neap +2 | 4.7 | 08:00 - wind speed (mhp) 25 (drops to 14 @ 12:00, up to 26 @16:00, down to 21 @ 08:00), Wind direction NW (, Temperature (Day @ 08:00) 13-11°C, (night @ 20:00) 12-11°C
9-10/11/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-12:00 (38-37), 12:00-17:00 (37), 17:00-20:00 (37-38), 20:00-02:00 (38-37), 02:00 step increase from 37 to 38, 02:00-07:00 (38-37), 07:00-08:00 (37-37.5) | Neap | 2.8 | 08:00 - wind speed (mhp) 19 (increase to 25mph by 11:00, then gradual decrease to 10mph by 00:00, followed by a spike to 20mph at 04:00 before increase to 24mph at 08:00), Wind direction E (change from E to S to W), Temperature (Day @ 08:00) 13°C, (night) decrease to 12°C
10-11/11/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-22:00 (37), 22:00-23:30 (31), 23:30-00:00 (16), 00:00-03:00 (8), 03:00-05:00 (13), 05:00-05:30 (25), 05:30-06:30 (34), 06:30-08:00 (38) | Neap +1 | 3.6 | 08:00 - wind speed (mhp) 23 (stable, slight fluctuations until 16:00, increase to 32mph), Wind direction SW (change from SW to S), Temperature (Day @ 08:00) 12°C (until 16:00 then gradual increase to 14°C), (night) increase from 12°C to 14°C
23-24/11/20 | 08:00-08:00 | AM+AS | OMR CW | 00:00-04:00 (16), 04:00-06:00 (38), 06:00-23:30 (37-38), 23:30-00:00 (16) | Neap -1 | 2.9 | 08:00 - wind speed (mhp) 21 (increases to 32 mph at 22:00 then decrease to 25 mph), Wind direction S (move more westerly through first 12 hrs then returns southerly), Temperature (Day @ 08:00) 11°C (increase to 12 then decrease back to 11 by 18:00), (night) 12°C (fluctuate between 12 and 13) | Repairs to drum screen 2
24-25/11/20 | 08:00-08:00 | AM+AS | OMR CW | 00:00-04:30 (8), 04:30-06:30(4 step increase to 38), 06:30-22:00 (38), 22:00-23:00 (decrease to 31), 23:00-00:00 (decrease to 8) | Neap +/-0 | 3.2 | 08:00 - wind speed (mhp) 28 (fluctuate between 28 and 34 until 20:00, decrease to 9, fluctuate from 12-20 for remainder), Wind direction S (Southerly until 20:30 change to NW for remaining), Temperature (Day @ 08:00) 10°C (increase to 13 until 20:30), (night) 9°C (drops to 10 at 20:30 decrease to 9 overnight)
30-1/12/20 | 08:00-08:00 | AM+AS | OMR CW | 08:00-11:00 (decrease 38-36.5), 11:00-15:00 (increase 36.5 to 38.5), 15:00-00:00 (decrease 38.5-36.5), 00:00-04:00 (increase 36.5-38.5), 04:00-08:00 (decrease 38.5-37) | Spring - 1 | 5.4 | 08:00 - wind speed (mhp): 17 (increase 30 by 16:00, decrease to 12 by 08:00), Wind direction: W (from W to N by 21:00, Northerly for remainder), Temperature (Day @ 08:00) 11°C (fluctuates 11 and 12 until 22:00), (night) 9°C (from 22:00 to 04:00 decrease from 11 to 9 then remains)
1-2/12/20 | 08:00-08:00 | AM+AS | OMR CW | 00:00-22:30 (37-38), 22:30-23:30 (decrease to 30), 23:30-00:00 (decrease to 15) | Spring +/- 0 | 5.4 | 08:00 - wind speed (mhp): 12 (drop to 1 by 11:00, increase to 11 by 13:00. Increase to 20 by 00:30, drop to 5 at 02:00 to 20 by 03:30, drop to 8 at 5:30 return to 19), Wind direction: N (Move N to NW), Temperature (Day @ 08:00) 10°C (remains throughout day), (night) 11°C (increase from 10-12 during 18:00-00:00 then increase to 11 by 02:00 and remains) | Repairs to drum screen 2 were being conducted so it was not operational
7-8/12/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-16:00 (37.5), 16:00-19:00 (38.5). 19:00-00:00 (37.5), 00:00-01:00 (38.5), 01:00-04:00 (38), 04:00-07:00 (38.5), 07:00-08:00 (38) | Spring -2 | 3.7 | 08:00 - wind speed (mhp): 15 (decrease gradually, large fluctuations to 5mph @ 18:30, general increase large fluctioations through rest of period 25 mph @ 08:00), Wind direction: E (gradual move from E to N to W), Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 5°C (increase from 5 to 8 by 15:00 decrease to 6 by 20:00), (night) 3°C (increase to 7 by 22:00 holds until 8:00) | Repairs to drum screen 2 were being conducted so it was not operational. fish spray filters cleaned. Work on cranes by MCW intake
8-9/12/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-23:30 (38), 23:30-00:00 (8), 00:00-05:00 (8), 05:00-06:30 (step increase 8 to 38), 06:30-08:00 (38) | Spring -1 | 3.6 | 08:00 - wind speed (mhp): 25 (gradual increase to 30 by 19:00, decrease to 12 by 08:00), Wind direction: W, Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 8°C (increase to 9 by 17:00), (night) 9°C (decrease to 8 by 00:00 holds until 8:00) | Repairs to drum screen 2. fish spray filters cleaned. Work on cranes by MCW intake
14-15/12/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-21:30 (37-38), 21:30-22:00 (step decrease 23), 22:00-05:00 (decrease to 7-8), 05:00-06:00 (step increase 26), 06:00-08:00 (step increase 38) | Spring - 1 | 6.4 | 08:00 - wind speed (mhp): 40 (16:30 drop to 23 @17:00, remained stable for rest of period), Wind direction: SW (moves S), Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 12°C (fluctuate 9-12), (night) 10°C (fluctuate 9-11) | Repairs to drum screen 2. fish spray filters cleaned. Work on cranes by MCW intake
15-16/12/20 | 08:00-08:00 | AM+AS | HC OMR | 08:00-23:00 (37-38), 23:00-23:30 (30), 23:30-00:00 (15), 00:00-04:00 (8), 04:00-06:00 (8-38), 06:00-08:00 (38). | Spring +/- 0 | 6.3 | 08:00 - wind speed (mhp): 25 (fluctuation between 18-31 until 17:00, gradual increase 46 @ 04:00, Drops to 33 for remainder), Wind direction: SW (moves SE then returns SW), Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 11°C (fluctuate 11-9 until 10:00, remained 11), (night) 11°C (11 until 05:00, increase to 12 for remainder) | Repairs to drum screen 2. fish spray filters cleaned. Work on cranes by MCW intake

## Total biomass_20
MAIN CATCH BIOMASS + TRASH BIOMASS
Species (cells linked to species list) | 2020-01-13 | 2020-01-14 | 2020-01-27 | 2020-02-11 | 2020-02-12 | 2020-02-17 | 2020-02-18 | 2020-03-02 | 2020-03-03 | 2020-03-16 | 06-08/04/2020 | 20-22/04/2020 | 05-07/05/2020 | 11-13/05/2020 | 26-28/05/2020 | 02-04/06/2020 | 22-24/06/2020 | 2020-07-13 | 2020-07-14 | 2020-07-27 | 2020-07-28 | 2020-08-03 | 2020-08-04 | 2020-08-05 | 2020-09-02 | 2020-09-14 | 2020-10-06 | 2020-10-07 | 2020-10-12 | 2020-10-13 | 2020-11-09 | 2020-11-10 | 2020-11-23 | 2020-11-24 | 2020-11-30 | 2020-12-01 | 2020-12-07 | 2020-12-08 | 2020-12-14 | 2020-12-15
Pogge | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 4 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 0 | 0 | 27 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 66 | 67
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 62 | 0 | 0 | 0 | 0 | 44 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 5948 | 2573 | 1362 | 22340 | 7324 | 5621 | 3415 | 1697 | 2202 | 4278 | 865 | 28 | 24 | 24 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 88 | 1 | 22 | 2 | 12 | 16 | 142 | 89 | 262 | 254 | 48 | 239 | 117 | 158 | 461 | 528
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 18 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 37 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 1 | 0 | 0 | 15 | 20 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 80 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 1 | 11 | 7 | 19 | 13 | 26 | 13 | 103 | 80 | 15 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 13 | 0 | 8 | 2 | 0 | 1 | 23 | 4 | 3 | 6 | 2 | 7 | 29 | 4 | 1 | 3
Herring | 600 | 5 | 9 | 832 | 77 | 18 | 0 | 11 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 134 | 4 | 0 | 0 | 0
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 1715 | 762 | 26 | 117 | 56 | 301 | 171 | 734 | 368 | 22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 16 | 1 | 2 | 1 | 102 | 3 | 32 | 12 | 13 | 21 | 50 | 18 | 20 | 36
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 64 | 57 | 0 | 0 | 17 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 12 | 0 | 19 | 21 | 14 | 25 | 18 | 84 | 0 | 18
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 14 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 578 | 33 | 361 | 60 | 777 | 25 | 41 | 61 | 98 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 64 | 69 | 22 | 0 | 26 | 0 | 122 | 121 | 228 | 222 | 0 | 40 | 31 | 387
Bib | 170 | 74 | 0 | 2351 | 445 | 155 | 0 | 0 | 0 | 0 | 0 | 59 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 42 | 0 | 0 | 79 | 0 | 0 | 235 | 241
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 74 | 138 | 18 | 2640 | 100 | 49 | 136 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 14 | 0 | 159 | 41 | 0 | 0 | 21 | 0 | 82 | 68 | 22 | 40 | 32 | 11 | 54 | 0
Poor cod | 90 | 4 | 24 | 36 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30 | 0 | 0 | 93 | 14 | 65 | 34 | 8 | 21 | 23 | 0 | 270 | 436
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 356 | 0 | 0 | 6192 | 1197 | 260 | 0 | 67 | 0 | 60 | 53 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 28 | 0 | 0 | 21 | 2 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 3 | 6 | 46 | 49 | 26 | 9 | 26 | 120 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 | 0 | 4 | 4 | 0 | 2 | 7 | 4 | 7 | 1 | 0 | 4 | 0 | 0 | 4 | 7
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Black goby | 0 | 0 | 0 | 32 | 65 | 7 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0
Common goby | 1 | 2 | 0 | 7 | 7 | 9 | 5 | 1 | 3 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 1 | 1 | 2 | 1 | 2 | 1 | 1 | 1 | 3 | 1 | 2 | 1 | 1 | 0 | 1 | 0 | 1 | 4
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 0 | 0 | 0 | 0 | 5 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 2 | 2 | 1 | 2 | 1 | 0 | 1
Rock goby | 47 | 22 | 6 | 60 | 101 | 22 | 8 | 17 | 38 | 26 | 3 | 1 | 7 | 9 | 0 | 2 | 0 | 4 | 4 | 11 | 11 | 20 | 0 | 7 | 3 | 15 | 100 | 29 | 2 | 0 | 22 | 6 | 7 | 15 | 23 | 12 | 16 | 1 | 13 | 66
Sand goby | 75 | 36 | 47 | 2132 | 937 | 398 | 278 | 38 | 93 | 24 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 4 | 0 | 22 | 20 | 1 | 1 | 20 | 1 | 26 | 13 | 9 | 7 | 9 | 12 | 16 | 59
Transparent goby | 1 | 0 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 527 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 7 | 3 | 0 | 69 | 52 | 16 | 10 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 9 | 1 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 88 | 0 | 1 | 0 | 3 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 3 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 150 | 62 | 31 | 2178 | 680 | 164 | 329 | 77 | 163 | 85 | 31 | 4 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 336 | 1 | 0 | 0 | 44 | 0 | 8 | 9 | 3 | 6 | 0 | 0 | 0 | 0
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 0 | 0 | 0 | 1618 | 0 | 0 | 0 | 12 | 0 | 22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 67 | 0 | 0 | 82 | 0 | 0 | 0 | 1 | 49 | 74
Mullet indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thin lipped grey mullet | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 15 | 0 | 0 | 0 | 4 | 11 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 12 | 0
Dab | 0 | 0 | 0 | 0 | 0 | 85 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 114
Flounder | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plaice | 0 | 0 | 0 | 0 | 107 | 0 | 0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 230 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 1214 | 854 | 575 | 1739 | 2287 | 1144 | 748 | 399 | 576 | 2165 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 128 | 0 | 0 | 0 | 0 | 0 | 107 | 0 | 1181 | 624 | 0 | 4149 | 8879
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 79 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 1 | 0 | 0 | 1 | 5 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 3 | 2 | 2 | 3 | 1 | 18 | 1 | 2 | 25 | 0 | 2 | 3 | 8
Nilsson's pipefish | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 4 | 0 | 0 | 6 | 4 | 4 | 4 | 12 | 14 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 1 | 0 | 1 | 0 | 16 | 1 | 1 | 5 | 7 | 0 | 2 | 15
Worm pipefish | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 163 | 18 | 0 | 399 | 86 | 0 | 0 | 42 | 0 | 29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 36 | 212 | 26 | 41 | 23 | 32 | 0 | 19 | 75
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 51 | 0 | 0 | 0 | 33 | 0
John dory | 0 | 0 | 0 | 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Note on L2: Watts, Karen: 3 8HR DAYS ONLY
Note on M2: Watts, Karen: 3 8HR DAYS ONLY
Note on N2: Watts, Karen: 3 8HR DAYS ONLY
Note on O2: Watts, Karen: 3 8HR DAYS ONLY
Note on P2: Watts, Karen: 3 8HR DAYS ONLY
Note on Q2: Watts, Karen: 3 8HR DAYS ONLY
Note on R2: Watts, Karen: 3 8HR DAYS ONLY

## Total abundance_20
MAIN CATCH ABUNDANCE + TRASH ABUNDANCE
Species (cells linked to species list) | 2020-01-13 | 2020-01-14 | 2020-01-27 | 2020-02-11 | 2020-02-12 | 2020-02-17 | 2020-02-18 | 2020-03-02 | 2020-03-03 | 2020-03-16 | 06-08/04/2020 | 20-22/04/2020 | 05-07/05/2020 | 11-13/05/2020 | 26-28/05/2020 | 02-04/06/2020 | 22-24/06/2020 | 2020-07-13 | 2020-07-14 | 2020-07-27 | 2020-07-28 | 2020-08-03 | 2020-08-04 | 2020-08-05 | 2020-09-02 | 2020-09-14 | 2020-10-06 | 2020-10-07 | 2020-10-12 | 2020-10-13 | 2020-11-09 | 2020-11-10 | 2020-11-23 | 2020-11-24 | 2020-11-30 | 2020-12-01 | 2020-12-07 | 2020-12-08 | 2020-12-14 | 2020-12-15
Pogge | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 549 | 342 | 129 | 2282 | 837 | 590 | 383 | 176 | 224 | 390 | 78 | 3 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 108 | 1 | 13 | 2 | 9 | 12 | 17 | 8 | 26 | 23 | 10 | 33 | 25 | 17 | 62 | 95
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 1 | 0 | 0 | 2 | 4 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 15 | 9 | 10 | 8 | 5 | 32 | 16 | 201 | 133 | 24 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 32 | 0 | 24 | 11 | 0 | 2 | 46 | 6 | 6 | 9 | 5 | 9 | 73 | 9 | 2 | 7
Herring | 76 | 1 | 1 | 48 | 13 | 3 | 0 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0 | 0
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 1244 | 739 | 32 | 122 | 62 | 281 | 156 | 604 | 310 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 36 | 1 | 2 | 1 | 112 | 5 | 40 | 17 | 16 | 30 | 62 | 26 | 28 | 48
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 2 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 0 | 1
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 10 | 2 | 7 | 2 | 12 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 3 | 1 | 0 | 1 | 0 | 4 | 4 | 7 | 6 | 0 | 1 | 2 | 12
Bib | 2 | 2 | 0 | 10 | 4 | 2 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 2 | 0 | 0 | 2 | 4
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 2 | 3 | 1 | 11 | 3 | 2 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 5 | 4 | 0 | 0 | 2 | 0 | 3 | 2 | 1 | 1 | 2 | 1 | 4 | 0
Poor cod | 2 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 6 | 2 | 5 | 3 | 1 | 3 | 2 | 0 | 21 | 31
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 5 | 0 | 0 | 39 | 7 | 3 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 1 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 1 | 1 | 9 | 7 | 5 | 1 | 3 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 2 | 2 | 0 | 1 | 2 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 2
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Black goby | 0 | 0 | 0 | 22 | 14 | 3 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Common goby | 2 | 2 | 0 | 19 | 14 | 17 | 8 | 2 | 2 | 2 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 1 | 2 | 2 | 1 | 6 | 1 | 2 | 1 | 4 | 1 | 3 | 2 | 1 | 0 | 1 | 0 | 1 | 5
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 0 | 0 | 0 | 0 | 2 | 3 | 3 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 4 | 2 | 4 | 4 | 5 | 1 | 2 | 1 | 0 | 1
Rock goby | 22 | 5 | 3 | 105 | 50 | 12 | 9 | 5 | 6 | 4 | 3 | 1 | 5 | 5 | 0 | 1 | 0 | 4 | 3 | 3 | 3 | 3 | 0 | 2 | 4 | 4 | 25 | 10 | 5 | 0 | 7 | 1 | 6 | 6 | 12 | 5 | 8 | 1 | 7 | 15
Sand goby | 27 | 15 | 14 | 1001 | 460 | 157 | 101 | 18 | 41 | 10 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 4 | 0 | 28 | 29 | 1 | 1 | 12 | 1 | 20 | 7 | 4 | 3 | 6 | 5 | 11 | 30
Transparent goby | 1 | 0 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 12 | 5 | 1 | 2 | 2 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 1 | 1 | 0 | 32 | 25 | 10 | 5 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 2 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 1 | 0 | 3 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 18 | 9 | 5 | 130 | 87 | 25 | 29 | 16 | 30 | 14 | 5 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 2 | 3 | 1 | 1 | 0 | 0 | 0 | 0
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 2 | 3
Mullet indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thin lipped grey mullet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 2 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
Dab | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Flounder | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plaice | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 4 | 3 | 1 | 4 | 8 | 7 | 3 | 1 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 3 | 1 | 0 | 7 | 16
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 1 | 0 | 0 | 2 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 6 | 7 | 3 | 5 | 4 | 1 | 4 | 1 | 4 | 3 | 0 | 4 | 4 | 2
Nilsson's pipefish | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 5 | 0 | 0 | 4 | 2 | 2 | 1 | 1 | 3 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 2 | 0 | 4 | 1 | 1 | 2 | 1 | 0 | 2 | 3
Worm pipefish | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 6 | 1 | 0 | 14 | 4 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 1 | 10 | 2 | 2 | 1 | 1 | 0 | 1 | 3
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
John dory | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Note on L2: Watts, Karen: 3 8HR DAYS ONLY
Note on M2: Watts, Karen: 3 8HR DAYS ONLY
Note on N2: Watts, Karen: 3 8HR DAYS ONLY
Note on O2: Watts, Karen: 3 8HR DAYS ONLY
Note on P2: Watts, Karen: 3 8HR DAYS ONLY
Note on Q2: Watts, Karen: 3 8HR DAYS ONLY
Note on R2: Watts, Karen: 3 8HR DAYS ONLY

## Entrainment_21
Taxa | 2021-04-20 | 2021-04-29 | 2021-05-11 | 2021-05-24 | 2021-06-08 | 2021-06-23 | 2021-07-08 | 2021-07-27 | 2021-08-17
Sand smelt | - | - | - | 39712 | 53975 | 56010 | 2623 | - | -
Two-spotted clingfish | 1806 | 1138 | 988 | 1135 | 1963 | 2000 | 874 | - | -
Goby family | 45146 | 35264 | 241981 | 383505 | 118744 | 141025 | 69062 | 8066 | 14084
Indeterminate | 903 | 15926 | - | 1135 | - | 2000 | 6119 | 1008 | -
Norway/ Longspined bullhead | 3612 | 3413 | - | - | - | - | - | - | -
Herring | 2709 | - | - | - | - | - | - | - | -
Tompot | 903 | - | 988 | 2269 | 981 | - | 3497 | - | -
Blenny
Clupeid family | 903 | 2275 | - | - | 981 | - | - | - | -
Dragonet family | - | 4550 | - | - | - | - | - | - | -
Yarrell’s blenny | - | 2275 | - | - | - | - | - | - | -
Dab | - | 2275 | - | - | - | - | - | - | -
Flounder | - | 1138 | 988 | - | - | - | - | - | -
Whiting | - | 2275 | - | - | - | - | - | - | -
Sprat | - | - | 1975 | - | - | - | - | - | -
Shanny | - | - | 1975 | 3404 | 6869 | - | - | - | -
Montagu’s seasnail | - | - | 988 | - | 981 | - | - | - | -
Bass | - | - | - | 1135 | 981 | - | - | - | -
Blenny family | - | - | - | 1135 | - | 12002 | - | - | -
Common | - | - | - | 1135 | - | - | - | - | -
dragonet
Ballan wrasse | - | - | - | - | - | - | - | 1008 | -
eggs | 34311 | 65977 | 29630 | 26097 | 26497 | 4001 | 5245 | 1008 | 0

## Metadata_21
Survey Number | Survey Date | Sample time | Net operatives | Sampling staff | Station flow (m3/Sec) | Spring/Neap | Max tidal Range (m) | Weather Obs | Comments
1 | 2021-01-25 | 2021-01-26 | 08:00-08:00 | AM + AS | 08:00-14:00 (steady increase 31-33), 14:00-15:00 (step increase 33-34), 15:00-08:00 (step increase 34-38) | Spring + 1 | 3.76 | 08:00 - wind speed (mhp): 17 (decreased 17-13 @ 11:00, increase 18 until 18:00, decrease 14 but 21:00, flutuate 12-21 until 03:00, general increase until 08:00. Large fluctuations up to 25), Wind direction: NW (moves Nw to W to S thorugh period), Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 6°C (gradually increase to 7.5 by 21:00), (night) 7°C (fluctuate 7-8) | Drum screen 2 isolated, remedial repairs. Work on MCw intake crane, Work on drum screens 1 & 4, Fish spray filters, Fish protection pump and alarm, water intake temp calibration
2 | 2021-01-26 | 2021-01-27 | 08:00-08:00 | AM + AS | 08:00-12:00 (38-38.5), 12:30-18:00 (38.5-37.5), 18:00-01:30 (37.5-38.5), 01:30-06:30 (38.5-37.5), 06:30-08:00 (37.5-38) | Spring + 2 | 4.47 | 08:00 - wind speed (mhp): 25 (increase to 35 by 10:00, decrease gradually to 5 @ 21:00, increase to 16 by 00:00, remained with fluctuation to 9 for rest of period), Wind direction: S (moves towards W by 16:00, remains for rest of period, Cloud (%): n/a. Rainfall (mm): n/a. Temperature (Day @ 08:00) 7°C (gradually increase to 10 by 15:00, decrease to 9-9.5 fluctuates), (night) 9°C (fluctuate 9-9.5 throught night) | Drum screen 2 isolated, remedial repairs. Work on MCw intake crane, Work on drum screens 1 & 4, Fish spray filters, Fish protection pump and alarm, water intake temp calibration
3 | 2021-02-15 | 2021-02-16 | 08:00-08:00 | Am + AS | 08:00-10:00 (step increase 8-38), 10:00-22:30 (fluctuates 37-38), 22:30-23:00 (step decrease 32), 23:00 - 23:30 (step decrease 24), 23:30-03:30 (step decrease 8), 03:30-05:00 (step increase 12), 05:00-06:30 (step increase 38), 06:30-08:00 (38) | Neap +-0 | 5.84 | 08:00 - wind speed (mhp): 24 (remains 25 until 21:00, increase 35 at 23:00, decrease 23 at 08:00), Wind direction: S (moves SW until 21:00, S for remainder), Cloud (%): 90%. Rainfall (mm): 1. Temperature (Day @ 08:00) 9.3°C (increase to 10 by 12:00, decrease to 9 by 18:00), (night) 9.5°C (increase 21:00-22:00 from 9 to 10, remain 10 until 02:00, drop 9 before increase to 9.5 and remains) | Work on MCW crane, cleaning of fish spray filters, small leak in U21 MCW outlet line
4 | 2021-02-22 | 2021-02-23 | 08:00-08:00 | AM + AS | 08:00-08:30 (34.5 m3/s), 08:30-08:00 (step increase 38.5, fluctuates between 38-39) | Spring - 1 | 5.49 | 08:00 - wind speed (mhp): 0.5 (steady increase from 0.5-40), Wind direction: SE (moved S by 12:00 then back to SE at 19:00 then S remainder), Cloud (%): 10% (increased through night to 100%) Rainfall (mm): 0. Temperature (Day @ 08:00) 7.5°C (increase to 9 by 10:00, flucuate 8.5-9.5 by 16:00, drop to 8 at 18:00), (night) 9°C (increase from 8 at 18:00 to 10 at 08:00) | Removal of one of the MCW intake Temperature probes (due to be reinstalled on 22/02/2021) Fish detterent Speaker maintenance Fish Spray Filters Cleaned Crane investigation at MCW inlet
5 | 2021-02-23 | 2021-02-24 | 08:00-08:00 | AM + AS | 08:00-23:00 (38 m3/s), 23:00-23:30 (step decrease 24 m3/s), 23:30-00:30 (step decrease to 16m3/s), 00:30-05:00 (step decrease to 8m3/s), 05:00-06:00 (step increase to 12m3/s), 06:00-08:00 (step increase to 16m3/s) | Spring +-0 | 5.76 | 08:00 - wind speed (mhp): 40 (gradually dropped between 08:00 and 06:00 to 29, decrease rapidly to 12 mph at 08:00), Wind direction: S (S until 06:00 then moves to SW by end), Cloud (%): 100%, Rainfall (mm): 9. Temperature (Day @ 08:00) 10°C (increase to 11 by 11:00, gradually decrease through period, 9 at 08:00), (night@ 04:00) 7°C (increase 10.5 to 11 by 21:00, decrease rest of period to 9 at 08:00) | One of the MCW intake Temperature probes replaced, Fish deterrent Speaker maintenance, Fish Spray Filters Cleaned, Crane investigation at MCW inlet
6 | 2021-02-24 | 2021-02-25 | 08:00-08:00 | AM + AS | 08:00-11:00 (16), 11:00-12:30 (step increase 20), 12:30-13:15 (step decrease 16), 13:15-14:00 (step decrease 21), 14:00- 15:30 (four step increase, 38), 15:30-20:30 (38), 20:30-21:00 (three step increase, 8), 21:00-05:00 (8), 05:00-06:30 (step increase 21), 06:30-07:00 (step increase 28), 07:00-08:00 (step increase 35). | Spring + 1 | 5.86 | 08:00 - wind speed (mhp): 14 (increased to 35 by 11:00, decease to 25 at 13:30, increased o 32 at 14:30 and 16:00, gradually increase to 21 by 23:00, fluctuate 10-16 between 23:00-08:00), Wind direction: SW (moves W throughout then fluctuates between W and SW), Cloud (%): 100% (changes to clear overnight), Rainfall (mm): 7 (roughly). Temperature (Day @ 08:00) 9°C (increase to 11 by 11:00, remained until 14:30, then decrease to 8), (night@ 02:00) 8.5°C (fluctuate between 8 and 9) | One of the MCW intake Temperature probes replaced, Fish deterrent Speaker maintenance, Fish Spray Filters Cleaned, Crane investigation at MCW inlet
7 | 2021-03-09 | 2021-03-10 | 08:00-08:00 | AM + AS | 08:00-08:00 fluctuates between 38 and 39 m3/s | Neap + 3 | 3.9 | 08:00 - wind speed (mhp): 17 (steady increase in speed to 40mph at 02:00, it then gradually decreased to 29mph by 08:00), Wind direction: SW (the direction moved slightly towards S at 13:00, and remained at SSW for rest of period), Cloud (%): 60% (increased to 100% for majority of period), Rainfall (mm): 8 (rough value, heavy fall in second half of period). Temperature (Day @ 08:00) 8°C , (night@ 00:00) 8.5°C (increased to 9 by 03:00) | Drum screen 3 tripping, repairs to MCW crane, cleaning of fish spray filters, Roughly half of the bar screens have been lifted for cleaning. Maintenance on drumscreen.
8 | 2021-03-22 | 2021-03-23 | 08:00-08:00 | Carl | 08:00 - 10:30 (32.5-33.5), 10:30-17:00 (33.5-32), 17:00-23:00 (32-33.5), 23:00-00:45 (step increase 34.5), 00:45 - 01:30 (step decrease 32.5), 01:30-03:30 (step increase 34.5), 3:30-08:00 (34.5-35.5) | Neap + 1 | 2.34 | 08:00 - wind speed (mhp): 11 (general increase across 24hr period), Wind direction: SE (Changed S at 05:00, remained S for period), Cloud (%): 90% (remained cloudy for rest of period period), Rainfall (mm): 0. Temperature (Day @ 08:00) 7.5°C (gradual increase by 9C by 14:00), (night@ 00:00) 9°C | MCW Pump 1 tripped, work ongoing to replace, cleaning of fish spray filters
9 | 2021-03-23 | 2021-03-24 | 08:00-08:00 | Carl | 08:00-10:15 (35.5-36), 10:15-18:00 (gradual decrease 34.5), 18:00-23:00 (gradual increase 35.5), 23:00-08:00 (decrease 35) | Neap +2 | 2.42 | 08:00 - wind speed (mhp): 24 (fluctuates around 24mph until 18:00-decrease to 21 by 1:30. decrease to 9mph by 03:00, increase 18mph by 04:00. speed droppded to 11mph by 0530 and remained until 08:00), Wind direction: S (Direction moves SW throughout, change to W at 02:00, ack to Sw by end of period), Cloud (%): 90% (decreased through period by 50%), Rainfall (mm): 0. Temperature (Day @ 08:00) 9°C (gradual increase to 9.5 by 13:00, remained until 01:30), (night@ 00:00) 8.5°C (drops from 9.5 to 8 at 02:00 then increase to 9 by 08:00) | MCW Pump 1 tripped, work ongoing to replace, cleaning of fish spray filters, cleaning of large screen doors post survey
10 | 2021-04-19 | 2021-04-20 | 08:00-08:00 | Andy Smith | 08:00 - 11:00 Increase from 31.5 m3/s to 32.5m3/s 11:00 - 17:00 Decrease from 32.5 m3/s to 30.5 m3/s 17:00 - 23:30 Increase from 30.5 m3/s to 32.5 m3/s 23:30 - 05:00 Decrease from 32.5 m3/s to 31 m3/s 05:00 - 08:00 Remained at 31 m3/s | Neap -2 | 2.88 | 08:00 - Windspeed: increased from 7mph to 16mph by 12:00, then decreased to roughly 4.5mph for the rest of the period. 08:00 - Wind direction: Moved from Easterly to Southerly to Easterly over the period. 08:00 - temperature (day): Increased to 14°C by 17:00 then decreased to 10°C by 21:00. 08:00 - temperature (night): Decreased to 9°C by 08:00. | Cleaning of fsh spray filters
11 | 2021-04-20 | 2021-04-21 | 08:00-08:00 | Andy Smith | 08:00 - 12:30 31m3/s 12:30 - 12:45 Drop to 24m3/s before increasing sudenly to 28m3/s 12:45 - 14:30 28m3/s 14:30 - 00:00 Starts at 32m3/s before gradually decreasing to 31m3/s by 19:00, followed by an increase to 32m3/s 00:00 - 08:00 34m3/s | Neap -1 | 2.4 | 08:00 - windspeed: Fluctuated between 2 and 10mph until 16:00 before increasing to 14mph at 18:00 then gradually decreasing to 10mph by 08:00. 08:00 - wind direction: Moved from Northerly to Easterly throughout the period with some large variations throughout. 08:00 - temperature (day): Fluctuates between 10°C and 12°C. 08:00 - tenperature (night): Fluctuates between 10°C and 12°C. | Cleaning of fsh spray filters
12 | 2021-05-04 | 2021-05-05 | 08:00-08:00 | Andy Smith | 08:00 - 23:30 38m3/s 23:30 - 05:45 Step decrease to 24m3/s 05:45 - 07:00 Step increase to 32m3/s 07:00 - 08:00 Step increase to 34m3/s | Neap +-0 | 3.17 | 08:00 Windspeed 37mph NW Decrease to 14mph by 20:00, beforean increase back up to 37mph by 00:00 followed by a drop to 25mph by 08:00. Small fluctuations between N and W. 08:00 temperature 8.5°C Increased from 6°C to 9°C by 22:00, before decreasing to 7°C throughout the rest of the period | Issues with U41 MCW pump 2 Drum Screen 3 tripped and isolated to build scaffold for maintenance
13 | 2021-05-10 | 2021-05-11 | 08:00-08:00 | Andy Smith | 08:00 - 15:00 16m3/s 15:00 - 17:00 Increased to 33m3/s in three steps 17:00 - 00:00 gradually decreased to 30m3/s 00:00 - 05:00 Step down to 15m3/s followed by an increase to 16m3/s 05:00 - 08:00 Two step increases to 33m3/s at 08:00 | Spring + 1 | 5.37 | 08:00 windspeed 29mph SW. Increase to 38mph by 15:00 then a steady decrease to 15mph by 08:00. Fluctuated between S and W. Temperature day 11°C night 10°C. | Maintenance on Drum screen 3 and 4
14 | 2021-05-11 | 2021-05-12 | 08:00-08:00 | Andy Smith | 08:00 - 23:00 fluctuate between 30m3/s and 33m3/s 23:00 - 00:00 decrease to 7m3/s in three step changes 00:00 - 04:00 8m3/s 04:00 - 05:30 Increase to 33m3/s in three step changes 05:30 - 08:00 33m3/s | Spring + 2 | 5.45 | 08:00 windspeed 16mph S. Decreased to 9mph by 15:00, then spiked to 24mph at 18:00 followed by a decrease to 7mph at 22:00, there was then a general increase to 15mph by 08:00. Temperature day Fluctuated between 10 and 12°C night Fluctuated between 9 and 11°C | Maintenance on Drum screen 3 and 4
15 | 2021-05-24 | 2021-05-25 | 08:00-08:00 | Andy Smith | 08:00 - 11:00 23m3/s 11:00 - 15:30 step decrease to 8m3/s 15:30 - 17:00 multiple step increases to 29m3/s 17:00 - 19:00 29m3/s 19:00 - 23:00 step decrease to 24m3/s 23:00 - 00:00 step decreases to 8m3/s 00:00 - 08:00 multiple step increases to 32m3/s | Spring - 2 | 6.04 | 08:00 windspeed 11mph NW. Increase to 34mph followed by a drop to 16mph by 14:00. There was then a general increase to 30mph by 03:00 before decreasing to 20mph by 08:00. | Maintenance on Drum screen 3 Fish spray filters cleaned
16 | 2021-05-25 | 2021-05-26 | 08:00-08:00 | Andy Smith | 08:00 - 00:00 fluctuate between 30 and 33m3/s 00:00 - 00:30 step decrease to 15m3/s 00:30 - 05:30 step decrease to 8m3/s 05:30 - 06:30 three step increases to 29m3/s 06:30 - 08:00 29m3/s | Spring - 1 | 6.58 | 08:00: windspeed 18mph NW. Increased to 23mph by 12:00 followed by a decrease to 4mph by 18:00. There was then a general increase to 12mph by 08:00 Fluctuated between a maximum of 12.5 degrees and a minimum of 8 degrees throughout the period. | Maintenance on Drum screen 3 Fish spray filters cleaned
17 | 2021-06-08 | 2021-06-09 | 08:00-08:00 | Andy Smith & Andy Minion | 08:00 - 00:00 34 m3/s 00:00 - 01:00 step decrease to 12 m3/s 01:00 - 04:00 12 m3/s 04:00 - 06:00 Increase from 12 m3/s to 34 m3/s 06:00 - 08:00 34 m3/s | Spring - 2 | 4.62 | 08:00: windspeed 12 mph. General increase throughout period to 22 mph at 08:00. S wind moved slightly to SW. 08:00 - 14°C Increased to 15°C by 16:00 then decreased and remained at 14°C for the rest of the period
18 | 2021-06-14 | 2021-06-15 | 08:00-08:00 | Andy Smith & Andy Minion | 08:00 - 15:00 gradual decrease from 25 to 22m3/s 15:00 - 15:30 step increase to 30m3/s 15:30 - 00:00 general increase from 30 to 32m3/s 00:00 - 04:30 two step decreases to 7m3/s 04:30 - 08:00 multiple step increases to 32m3/s by the end of the period | Spring + 4 | 4.74 | 08:00 windspeed Increased to 14mph 12:00 before decreasing to 4mph between 20:00 and 08:00. Moved from NW through N to E throughout. 13 degrees Increased to 16°C by 14:00 then decreased to 14°C by 21:00. 08:00 - decreased from 14°C to 12°C by 03:00 then increased to 14°C by 08:00. Night temp: 14°C
19 | 2021-06-15 | 2021-06-16 | 08:00-08:00 | Andy Smith & Andy Minion | 08:00 - 11:00 32m3/s 11:00 - 12:00 34m3/s 12:00 - 14:30 23m3/s 14:30 - 15:30 27m3/s 15:30 - 17:30 step increases to 34m3/s 17:30 - 08:00 decrease from 34m3/s to 30m3/s before increasing to 32m3/s | Neap - 3 | 4.17 | 08:00: windspeed 14 mph, decreased to 8mph by 22:00 then increased to 16mph by the end of the period. SE moved to SW then S by end of the period. Cloud % 20, Clear throughout day then cloud cover increased at night. 14°C and 0.5 mm of rain at 08:00, light rain in the second half of the period. Temperature (day) increased to 17°C by 1900
20 | 2021-06-22 | 2021-06-23 | 08:00-08:00 | Andy Smith | 08:00 - 16:00 increase from 30 m3/s to 33 m3/s 16:00 - 21:30 decrease to 30 m3/s 21:30 - 00:00 step increase to 34 m3/s 00:00 - 01:00 step decrease to 20 m3/s 01:00 - 04:00 step decrease to 12 m3/s 04:00 - 05:30 multiple step increases to 38 m3/s 05:30 - 08:00 38 m3/s | Spring - 2 | 5.41 | 08:00 windspeed 8mph NE. Increase to 20mph by 12:00, then decreased throughout the rest of the period to 7mph. Moved from NE through N to W throughout the period. 08:00 temperature 13°C Increased to high's of roughly 20°C throughout the day | Maintenance on Drum screen 3
21 | 2021-06-23 | 2021-06-24 | 08:00-08:00 | Andy Smith | 08:00 - 11:00 Decrease from 38 m3/s to 37 m3/s 11:00 - 14:30 Increase from 37 m3/s to 38 m3/s 14:30 - 16:00 step decrease to 32 m3/s 16:00 - 17:00 step increase to 34 m3/s 17:00 Step increase to 38 m3/s 17:00 - 08:00 fluctuates between 38 m3/s and 36.5 m3/s | Spring - 1 | 5.88 | 08:00 windspeed 9mph W. decreased to 2mph by midnight, then increased to 4mph by 08:00. Wind direction moved from Westerley to Northerly. Temperature day Decreased from 13°C to 12°C, night Increased from 12°C to 14°C | Maintenance on Drum screen 3
22 | 2021-07-12 | 2021-07-13 | 08:00-08:00 | Andy Smith | 08:00 - 12:20 Flow decreased form 32.5 m3/s to 30 m3/s 12:20 - 16:00 Step increase to 33.5 m3/s 16:00 - 17:00 Step Increase to 38 m3/s 17:00 - 00:20 gradual decrease to 37.5 m3/s 00:20 Step decrease to 30.5 m3/s 00:20 - 05:00 decreased to 30 m3/s before increasing to 31 m3/s 05:00 - 06:30 Step increase to 34 m3/s 06:30 - 08:00 Step increase to 38 m3/s | Spring + 2 | 5.34 | 08:00 windspeed 5mph NE. Increased to 20 mph by 14:00, then generally decreased to 2 mph with some fluctuation by 08:00. Moved from NE to NW. 08:00 temperature 15°C. Increased from 15°C to 16°C then decreased to 15°C by 00:00Increased to 16°C by 08:00 | Maintenance on Drum screen 3 Replacement of pump for fish sprays
23 | 2021-07-13 | 2021-07-14 | 08:00-08:00 | Andy Smith | 08:00 - 14:30 Decrease from 37.5 m3/s to 36.5 m3/s 14:30 - 20:30 Increase to 37.5 20:30 - 03:00 Decrease to 36.5 03:00 - 08:00 Increase to 38 m3/s | Spring + 3 | 5.3 | 08:00 windspeed 5 mph NE. Decreased from 15mph to 2mph throughout the period, Moved from N to W then back to N. 08:00 temperature 16°C Increased to 18°C by 15:00 then decreased to 16°C by 00:00. | Maintenance on Drum screen 3 Replacement of pump for fish sprays
24 | 2021-07-26 | 2021-07-27 | 08:00-08:00 | Andy Smith | 08:00 - 14:00 Decrease from 38m3/s to 36m3/s 14:00 - 19:00 Increase from 36m3/s to 38.5m3/s 19:00 - 03:00 Decrease from 38.5m3/s to 36m3/s 03:00 - 06:30 Increase from 36m3/s to 39m3/s 06:30 - 08:00 Fluctuate around 38m3/s | Spring + 2 | 6.27 | 08:00 windspeed 2 mph NW. Increased to 21mph by 18:00 then generally decreased to 7mph by 08:00. NW for most of the period but chnges to SE at the end. 08:00 temperature 16°C Increased to 18°C by midday and fluctuated around this until 21:00 then decreased to 16°C with some fluctuation throughout the rest of the period. | Maintenance on Drum screen 3 following screen tripping Maintenance on fish sprays pumps Fish deflection maintenance Eel grass and weed build upon screens
25 | 2021-07-27 | 2021-07-28 | 08:00-08:00 | Andy Smith | 08:00 - 15:00 decreases from 38m3/s to 36m3/s 15:00 - 19:00 increases to 39m3/s 19:00 - 03:00 decreases to 36m3/s 03:00 - 08:00 increases to 39m3/s | Spring + 3 | 5.9 | 08:00 windspeed 7 mph SE. Decreased from 6.9mph at 08:00 to 2.3mph by 12:00, general increase from 12:00 until 06:00 reaching 11.5mph, dropping to 4.6mph by 08:00.Moved from South Eastery at 08:00 to westerly by 11:00, back to south easterly by 00:00. 08:00 temperature 16°C Fluctuates around 16°C for the whole period | Maintenance on Drum screen 3 following screen tripping Maintenance on fish sprays pumps Fish deflection maintenance Eel grass and weed build upon screens
26 | 2021-08-16 | 2021-08-17 | 08:00-08:00 | Andy Smith | 08:00 - 1:00 Fluctuate around 30m3/s 01:00 - 02:00 Decrease from 30m3/s to 24m3/s 02:00 - 05:20 Fluctuate around 16m3/s 05:20 - 05:40 Increase from 16m3/s to 31m3/s 05:40 - 08:00 Fluctuate around | Neap + 1 | 3.82 | Wind speed (mph) 8:00 26mph Decreased from 26mph at 08:00 to 9mph by 00:00. Increased up to 25mph by 08:00. Wind direction 8:00 NW NW for the whole period. Cloud (%) 8:00 70 Rainfall (mm) 8:00 2mm Temperature (day) 8:00 15°C General increase from 15°C at 08:00 to 16°C by midnight. Temperature (night) 0:00 16°C From 00:00 decreased from 16°C to around 15°C by 08:00. | Installation of spare fish pumps using temporary pipework improving availability
27 | 2021-08-17 | 2021-08-18 | 08:00-08:00 | Andy Smith | 08:00 - 01:00 Fluctuates around 30m3/s 01:00 - 01:10 decreases to 24m3/s 01:10 - 05:30 increases from 24m3/s to 32m3/s 05:30 - 08:00 fluctuates around 32m3/s | Neap + 2 | 3.31 | Wind speed (mph) 8:00 23 Decreased from 23mph to 9mph by 00:00. Increased to 16mph by 08:00. Wind direction 8:00 NW NW for the whole period. Cloud (%) 8:00 70 Rainfall (mm) 8:00 0 Temperature (day) 8:00 16°C General increase from 15°C to 16°C by midnight Temperature (night) 0:00 16°C Decreased from 16°C at 00:00 to 14°C by 08:00 | Installation of spare fish pumps using temporary pipework improving availability
28 | 2021-09-06 | 2021-09-07 | 08:00-08:00 | Andy Smith | 08:00 - 12:00 fluctuate around 33m3/s 12:00 - 15:30 decrease to 29m3/s 15:30 - 02:00 fluctuate around 31m3/s 02:00 - 02:30 drop to 28m3/s 02:30 - 08:00 steady increase to 32m3/s | Spring -1 | 5.93 | Wind speed (mph) 8:00 2 Decrease from 21mph at 08:00 to 3.4mph by 18:00. Increased back up to 17mph by 08:00. Wind direction 8:00 NE NE for most of the period but changes to SE near the period end. Cloud (%) 8:00 60 Rainfall (mm) 8:00 0 Temperature (day) 8:00 17°C Fluctuating between 17°C and 18°C Temperature (night) 0:00 16°C Decreased to 16°C with some fluctuation throughout the rest of the period. | Maintenance and cleaning on fish sprays and debris nosels and filters Eel grass and weed build up on screens resulting in deferral of survey
29 | 2021-09-20 | 2021-09-21 | 08:00-08:00 | Andy Smith | 08:00 - 13:00 general decrease from around 37.5m3/s to 36.5m3/s 13:00 - 16:00 increase to around 38m3/s 16:00 - 22:00 fluctuates around 38m3/s 22:00 - 01:30 decrease to around 36m3/s 01:30 - 05:00 increase to 38m3/s 05:00 - 08:00 fluctuate around 38m3/s | Spring | 6.3 | Wind speed (mph) 8:00 6.9mph Increased from 6.9mph at 08:00 to 13.8mph by 15:00, general decrease to 4.6mph by 08:00 Wind direction 8:00 SE SE from 08:00 to 00:00, changed to N for the rest of the period Cloud (%) 8:00 76 Rainfall (mm) 8:00 0 Temperature (day) 8:00 16°C Fluctuates around 16°C until 00:00 Temperature (night) 0:00 13.5 Decreased to 13.5°C by 08:00 | Low flows on fish and debris pump systems High eel grass quantities
30 | 2021-10-11 | 2021-10-12 | 08:00-08:00 | Andy Smith | 08:00 - 14:00 steady flow around 38m3/s 14:00 - 16:00 decrease to 36m3/s 16:00 - 20:00 increase to 38m3/s 20:00 - 05:30 fluctuates around 37m3/s 05:30 - 06:00 drop to 30m3/s 06:00 - 08:00 general increase to 31m3/s | Neap -2 | 5.32 | Wind speed (mph) 8:00 6.9mph Increased from 3mph at 08:00 to 6mph by 13:00, fluctuates around 6mph until 12:00am, increase to 8mph by 05:00 Wind direction 8:00 NW NW for most of the period Cloud (%) 8:00 50 Rainfall (mm) 8:00 0 Temperature (day) 8:00 7°C Increase from 7°C at 08:00 to 15°C by 11:00. Fluctuates around 15°C until 12:00am Temperature (night) 0:00 7°C Decrease to 7°C, fluctuates around this until 08:00 | Crossover on fish and debris pump systems High eel grass quantities
31 | 2021-10-12 | 2021-10-13 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 14:00 fluctuates around 32m3/s 14:00 - 15:30 increase to 34m3/s 15:30 - 16:00 increase to 37m3/s 16:00 - 08:00 fluctuates around 39m3/s | Neap - 1 | 4.45 | Wind speed (mph) 8:00 7mph Decreased from 7mph to 1mph by at 19:00. Increased to 6mph by 12:00am. Decrease to 3mph by 08:00. Wind direction 8:00 W W from 08:00 to 00:00, changed to NW for the rest of the period Cloud (%) 8:00 50 Rainfall (mm) 8:00 0 Temperature (day) 8:00 8°C 8°C at 08:00 increasing to 17°C by 15:30. Decrease to 11°C by 12:00am. Temperature (night) 0:00 9°C Fluctuates around 9°C until 08:00 | Cross over on fish and debris pump systems High eel grass quantities
32 | 2021-10-25 | 2021-10-26 | 08:00-08:00 | Andy Smith | 08:00 - 00:00 flow fluctuates around 38m3/s 00:00 - 01:00 flow decreases to 32m3/s 01:00 - 04:00 flow decreases to 23m3/s 04:00 - 06:00 increases to 39m3/s 06:00 - 08:00 flow fluctuates around 39m3/s | Neap -3 | 4.77 | Wind speed (mph) 8:00 23mph Wind fluctuates around 23mph from 08:00 to 00:00, wind increases to 25mph by 08:00. Wind direction 8:00 SW SW at 08:00, changes to S by 00:00 for the rest of the period Cloud (%) 8:00 84 Rainfall (mm) 8:00 0.8mm Temperature (day) 8:00 14°C Temperature fluctuates around 14°C until 00:00 Temperature (night) 0:00 15°C Temperature increases to 15°C by 05:00 until end of period | Cross over on fish and debris pump systems Debris sprays flushed through once a shift Eel grass risk low
33 | 2021-10-26 | 2021-10-27 | 08:00-08:00 | Andy Smith | 08:00 - 21:30 flow fluctuates around 38m3/s 21:30 - 23:00 flow decrease to 16m3/s 23:00 - 05:00 flow fluctuates around 17m3/s 05:00 - 07:00 flow increases to 38m3/s 07:00 - 08:00 flow stable at 38m3/s | Neap -2 | 4.14 | Wind speed (mph) 8:00 23mph General increase from 23mph to 37mph over entire period. Wind direction 8:00 SW SW from 08:00 to 07:00, changed to S for the rest of the period. Cloud (%) 8:00 100 Rainfall (mm) 8:00 0.7mm Temperature (day) 8:00 15°C Temperature fluctuates around 15°C. Temperature (night) 0:00 15°C Fluctuates around 15°C until 08:00 | Cross over on fish and debris pump systems Debris sprays flushed through once a shift Eel grass risk low
34 | 2021-11-15 | 2021-11-16 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 15:30 steady increase from 30m3/s to 33m3/s 15:30 - 22:10 decrease to 30m3/s 22:10 - 04:00 increased back to 33m3/s 04:00 - 08:00 steady decrease to 31m3/s | Neap +3 | 4.65 | Wind speed (mph) 8:00 23mph Fluctuates around 9.2mph and drops to 3.4 between 13:00 and 15:00. Increases to 11.5mph by 18:00. Wind direction 8:00 S S from 08:00 to 12:00, changed to N for the rest of the period. Cloud (%) 8:00 92%. Rainfall (mm) 8:00 0.4mm Temperature (day) 8:00 12°C Temperature fluctuates around 12°C. Temperature (night) 0:00 10°C | Cross over on fish and debris pump systems Debris sprays flushed through once a shift
35 | 2021-11-22 | 2021-11-23 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 02:00 flow fluctuates around 38m3/s 02:00 - 04:00 flow increases to 39m3/s 04:00 - 08:00 flow fluctuates around 39m3/s | Spring +3 | 5.02 | Wind speed (mph) 8:00 23.6mph General decrease over period to 12mph. Wind direction 8:00 NE and remains NE for whole period. Cloud (%) 8:00 10%. Rainfall (mm) 8:00 0.0mm Temperature (day) 8:00 6°C Temperature (night) 0:00 5°C | Cross over on fish and debris pump systems Debris sprays flushed through once a shift
36 | 2021-11-23 | 2021-11-24 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 14:00 temperature fluctuates around 38m3/s 14:00 - 17:30 Increase to 39m3/s 17:30 - 02:00 Decreases to 38m3/s 02:00 - 08:00 Fluctuates around 38m3/s for the rest of the period | Spring +4 | 4.64 | Wind speed (mph) 8:00 10mph General increase to 13mph by 12:00 decreases to 3.7 by 08:00. Wind direction 8:00 NE and moves to NW by end of period. Cloud (%) 8:00 18%. Rainfall (mm) 8:00 0.1mm Temperature (day) 8:00 5°C increasing to 11°C by midday. Temperature (night) 0:00 6°C | Cross over on fish and debris pump systems Debris sprays flushed through once a shift
37 | 2021-12-06 | 2021-12-07 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 13:00 flow decrease to 29m3/s 13:00 - 19:00 flow increases back to 34m3/s 19:00 - 21:00 decrease to 16m3/s 21:00 - 04:00 flow fluctuates around 15m3/s 04:00 - 07:00 increase to 21m3/s 07:00 - 08:00 decrease back to 17m3/s | Spring + 2 | 6.64 | Wind speed (mph) 08:00 26 mph General increase to 32 mph by 12:00, decrease to 22mph by midnight. Fluctuates around this for the rest of the period. Wind direction 08:00 NW moving to NE by the end of the period.Temperature (day) 08:00 8°C Temperature fluctuates around 8°C. Temperature (night) 00:00 6°C Temperature decreases to 6°C. | Cross over on fish and debris pump systems Debris sprays flushed through once a shift
38 | 2021-12-08 | 2021-12-09 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 20:00 flow increases to 35m3/s 20:00 - 03:00 flow decreases to 30m3/s 03:00 - 05:00 flow increases to 38m3/s 05:00 - 08:00 flow fluctuates around 38m3/s | Spring + 3 | 6.27 | Wind speed (mph) 08:00 31 mph General increase from 31mph to 35mph by midnight. Decrease to 24mph by end of period. High wind gusts of 68mph. Wind direction 08:00 SW moving to NW by the end of the period. Temperature (day) 08:00 8°C Temperature increases to 9°C by midday. Temperature (night) 00:00 6°C Temperature decreases to 6°C. | Cross over on fish and debris pump systems Debris sprays flushed through once a shift
39 | 13/12/2021 | 14/12/2021 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 17:00 Flow unstable mainly fluctuating around 31m3/s 17:00 - 08:00 Flow stable around 38m3/s | Neap +2 | 3.59 | Wind speed (mph) 08:00 7 mph General increase from 7mph to 17mph by miday. Decrease to 4mph by end of period. Wind direction 08:00 SE moving to W by the 21:00. Move to E by end of period. Temperature (day) 08:00 8°C Temperature increases to 12°C by midday. Temperature (night) 00:00 8°C Temperature decreases to 7°C by end of period. | Debris sprays flushed through once a shift. Issues with U11 and U21 Flowmeter affecting MCW total flow readings.
40 | 14/12/2021 | 15/12/2021 | 08:00-08:00 | Andy Smith | MCW Total Flow in last 24 hours: 08:00 - 13:00 flow decrease to 29m3/s 13:00 - 19:00 flow increases back to 34m3/s 19:00 - 21:00 decrease to 16m3/s 21:00 - 04:00 flow fluctuates around 15m3/s 04:00 - 07:00 increase to 21m3/s 07:00 - 08:00 decrease back to 17m3/s | Neap +3 | 3.85 | Wind speed (mph) 08:00 26 mph General increase to 32 mph by 12:00, decrease to 22mph by midnight. Fluctuates around this for the rest of the period. Wind direction 08:00 NW moving to NE by the end of the period. Temperature (day) 08:00 8°C Temperature fluctuates around 8°C. Temperature (night) 00:00 6°C Temperature decreases to 6°C. | Cross over on fish and debris pump systems Debris sprays flushed through once a shift

## Total abundance_21
MAIN CATCH ABUNDANCE + TRASH ABUNDANCE | 25-26/01/2021 | 26-27/01/2021 | 15-16/02/2021 | 22-23/02/2021 | 23-24/02/2021 | 24-25/02/2021 | 09-10/03/2021 | 22-23/03/2021 | 23-24/03/2021 | 19-20/04/2021 | 20-21/04/2021 | 04-05/05/2021 | 10-11/05/21 | 11-12/05/21 | 24-25/05/21 | 25-26/05/21 | 08-09/06/21 | 14-15/06/21 | 15-16/06/21 | 22-23/06/21 | 23-24/06/21 | 12-13/07/21 | 13-14/07/21 | 26-27/07/21 | 27-28/07/21 | 16-17/08/21 | 17-18/08/21 | 06-07/09/21 | 20-21/09/21 | 11-12/10/21 | 12-13/10/21 | 25-26/10/21 | 26-27/10/21 | 15-16/11/21 | 22-23/11/21 | 23-24/11/21 | 06-07/12/21 | 07-08/12/21 | 13-14/12/21 | 14-15/12/21
Species (cells linked to species list) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Pogge | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 65 | 97 | 66 | 19 | 6 | 9 | 37 | 103 | 122 | 117 | 115 | 344 | 28 | 29 | 20 | 2049 | 5 | 1 | 0 | 0 | 1 | 0 | 0 | 8 | 2 | 2 | 16 | 1 | 2 | 46 | 38 | 45 | 34 | 129 | 473 | 129 | 1809 | 2939 | 118 | 53
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 0 | 2
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 2 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 0 | 0
Clupeid indet | 2 | 0 | 0 | 2 | 1 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 70 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 12 | 0 | 0 | 0 | 6 | 0 | 0 | 20 | 0 | 0 | 0
Herring | 0 | 0 | 4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 2 | 111 | 100 | 1 | 2
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 0 | 1 | 198 | 21 | 1 | 3 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 10 | 0 | 1 | 16 | 1865 | 451 | 2302 | 1338 | 117 | 84
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 1 | 0 | 0 | 2 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 2 | 1 | 2 | 1 | 0 | 4 | 4
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 1 | 1 | 2 | 0 | 1 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 1 | 10 | 22 | 2 | 2
Bib | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 15 | 24 | 2 | 2
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 4 | 3 | 5 | 1 | 1 | 0 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 4 | 0 | 1 | 0 | 1 | 8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 7 | 28 | 6 | 5
Poor cod | 7 | 4 | 5 | 2 | 0 | 0 | 2 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 15 | 51 | 6 | 1
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 1 | 1 | 0
15-spined stickleback | 1 | 0 | 1 | 0 | 0 | 0 | 2 | 9 | 2 | 6 | 9 | 4 | 1 | 1 | 0 | 5 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 2 | 0 | 0 | 3 | 0 | 3 | 4 | 1 | 0 | 5 | 6 | 4 | 12 | 11 | 9 | 4
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0
Black goby | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 2
Common goby | 0 | 0 | 4 | 0 | 1 | 0 | 0 | 1 | 2 | 0 | 2 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 3 | 0 | 1 | 0 | 2 | 2 | 100 | 179 | 1 | 3
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 1 | 0 | 7 | 10 | 2 | 8 | 2 | 2 | 0 | 3 | 2 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 9 | 4 | 3 | 0 | 8 | 3 | 2 | 64 | 190 | 6 | 4
Rock goby | 0 | 1 | 3 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 3 | 4 | 0 | 0 | 2 | 1 | 0 | 1 | 3 | 2 | 0 | 1 | 0 | 0 | 3 | 6 | 1 | 7 | 2 | 6 | 18 | 5 | 86 | 95 | 1 | 7
Sand goby | 6 | 8 | 5 | 82 | 68 | 57 | 44 | 58 | 21 | 2 | 4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 5 | 0 | 1 | 30 | 5 | 8 | 10 | 2 | 5 | 0 | 517 | 3508 | 73 | 29
Transparent goby | 0 | 0 | 4 | 0 | 1 | 2 | 0 | 1 | 0 | 0 | 0 | 0 | 2 | 4 | 3 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 5 | 1 | 3 | 6 | 1 | 5 | 0 | 0 | 0
2-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 0 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 1 | 1 | 3 | 4 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 28 | 5 | 3
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 1 | 0 | 6 | 1 | 0 | 7 | 0 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 5 | 34 | 6 | 6
Mullet indet | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 0 | 1
Thin lipped grey mullet | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 17
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 2
Dab | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flounder | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Plaice | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 4 | 0 | 2 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 2 | 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 4 | 0 | 24 | 24 | 5 | 6
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 2 | 1 | 0 | 0 | 8 | 1 | 2 | 0 | 2 | 3 | 1 | 0 | 0 | 1 | 3 | 0 | 0 | 0 | 6 | 1 | 0 | 1 | 5 | 12 | 1 | 10 | 13 | 1 | 2
Nilsson's pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 8 | 0 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 2 | 2 | 1 | 3 | 6 | 2 | 2 | 2 | 1 | 0
Worm pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 7 | 1 | 3
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 7 | 0 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ling | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0

## Total biomass_21
MAIN CATCH BIOMASS + TRASH BIOMASS | 25-26/01/2021 | 26-27/01/2021 | 15-16/02/2021 | 22-23/02/2021 | 23-24/02/2021 | 24-25/02/2021 | 09-10/03/2021 | 22-23/03/2021 | 23-24/03/2021 | 19-20/04/2021 | 20-21/04/2021 | 04-05/05/2021 | 10-11/05/21 | 11-12/05/21 | 24-25/05/21 | 25-26/05/21 | 08-09/06/21 | 14-15/06/21 | 15-16/06/21 | 22-23/06/21 | 23-24/06/21 | 12-13/07/21 | 13-14/07/21 | 26-27/07/21 | 27-28/07/21 | 16-17/08/21 | 17-18/08/21 | 06-07/09/21 | 20-21/09/21 | 11-12/10/21 | 12-13/10/21 | 25-26/10/21 | 26-27/10/21 | 15-16/11/21 | 22-23/11/21 | 23-24/11/21 | 06-07/12/21 | 07-08/12/21 | 13-14/12/21 | 14-15/12/21
Species (cells linked to species list) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Pogge | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 57 | 0 | 0 | 0 | 0 | 24 | 32 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 846 | 1229 | 605 | 232 | 53 | 85 | 436 | 1289 | 1341 | 1301 | 1366 | 4382 | 318 | 301 | 204 | 24186 | 42 | 8 | 0 | 0 | 5 | 6 | 0 | 4 | 2 | 10 | 45 | 1 | 2 | 60 | 25 | 77 | 44 | 296 | 615 | 250 | 6361 | 10362 | 1354 | 612
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 142 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 0 | 0 | 75 | 0 | 93
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 21 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 12 | 0 | 0
Clupeid indet | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 7 | 0 | 0 | 0 | 2 | 0 | 0 | 2 | 0 | 0 | 0
Herring | 0 | 0 | 18 | 0 | 0 | 0 | 9 | 0 | 0 | 0 | 12 | 0 | 0 | 0 | 0 | 138 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 6 | 486 | 523 | 4 | 4
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sprat | 0 | 1 | 193 | 24 | 1 | 1 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 34 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 14 | 5 | 0 | 1 | 14 | 1574 | 380 | 2048 | 1226 | 119 | 101
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 34 | 0 | 0 | 61 | 0 | 0 | 0 | 15 | 0 | 0 | 61 | 0 | 0 | 0 | 0 | 0 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 5 | 0 | 0 | 33 | 0 | 30 | 0 | 61 | 45 | 35 | 57 | 0 | 112 | 191
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 60 | 37 | 108 | 0 | 35 | 0 | 0 | 319 | 0 | 0 | 0 | 0 | 0 | 0 | 18 | 51 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 90 | 0 | 34 | 573 | 939 | 70 | 139
Bib | 13 | 33 | 9 | 134 | 0 | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 110 | 0 | 0 | 962 | 1916 | 66 | 110
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 233 | 151 | 3735 | 17 | 3330 | 0 | 54 | 44 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 165 | 0 | 1 | 0 | 1 | 14 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 26 | 1 | 112 | 603 | 166 | 88
Poor cod | 78 | 54 | 54 | 8 | 0 | 0 | 39 | 8 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 17 | 0 | 0 | 158 | 633 | 45 | 7
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 0 | 17 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 157 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 166 | 48 | 23 | 0
15-spined stickleback | 2 | 0 | 4 | 0 | 0 | 0 | 18 | 80 | 33 | 62 | 113 | 50 | 9 | 15 | 0 | 46 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 2 | 0 | 0 | 4 | 0 | 6 | 11 | 3 | 0 | 15 | 17 | 18 | 35 | 42 | 34 | 12
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0
Black goby | 0 | 0 | 0 | 0 | 11 | 6 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 1 | 3 | 0 | 5 | 16
Common goby | 0 | 0 | 2 | 0 | 1 | 0 | 0 | 1 | 2 | 0 | 9 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 2 | 48 | 110 | 1 | 2
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 2 | 0 | 4 | 6 | 1 | 4 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 5 | 1 | 3 | 0 | 4 | 2 | 2 | 25 | 110 | 3 | 3
Rock goby | 0 | 2 | 5 | 0 | 9 | 15 | 12 | 10 | 4 | 0 | 0 | 0 | 1 | 0 | 49 | 7 | 0 | 0 | 4 | 2 | 0 | 6 | 8 | 9 | 0 | 3 | 0 | 0 | 26 | 22 | 1 | 44 | 2 | 18 | 40 | 16 | 167 | 195 | 1 | 21
Sand goby | 10 | 19 | 10 | 163 | 136 | 116 | 95 | 123 | 42 | 4 | 11 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 0 | 1 | 23 | 3 | 5 | 6 | 3 | 6 | 0 | 752 | 5328 | 185 | 84
Transparent goby | 0 | 0 | 2 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 1 | 1 | 2 | 1 | 68 | 0 | 0 | 0
2-spotted goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 12 | 0 | 0 | 0 | 0 | 0 | 22 | 42 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 60 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 169 | 63 | 0 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 84 | 5 | 164 | 1499 | 7 | 0 | 0 | 4 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 71 | 1100 | 30 | 19
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 97 | 0 | 171 | 23 | 0 | 115 | 0 | 47 | 302 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 3 | 20 | 196 | 1373 | 72 | 447
Mullet indet | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 0 | 1
Thin lipped grey mullet | 0 | 0 | 0 | 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 101 | 154
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 8 | 0 | 7 | 0 | 8 | 7 | 0 | 0 | 10
Dab | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flounder | 0 | 0 | 0 | 0 | 0 | 245 | 0 | 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 46
Plaice | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 67 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 110 | 0 | 52 | 70
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 53 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 2254 | 0 | 1103 | 0 | 1023 | 0 | 0 | 0 | 0 | 0 | 0 | 398 | 0 | 541 | 1225 | 5161 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 662 | 4 | 0 | 0 | 530 | 1176 | 0 | 14688 | 11031 | 2015 | 3341
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 27 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 34 | 0 | 0 | 61 | 22 | 32 | 0 | 0 | 83 | 19 | 36 | 0 | 31 | 15 | 5 | 0 | 0 | 1 | 21 | 0 | 0 | 0 | 4 | 1 | 0 | 1 | 1 | 30 | 29 | 10 | 24 | 1 | 39
Nilsson's pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 0 | 0
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 5 | 1 | 5 | 2 | 3 | 4 | 2 | 2 | 7 | 4 | 0
Worm pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 24 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 125 | 11 | 59
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 88 | 82 | 0 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ling | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0

## Entrainment_22
Name | 2022-04-06 | 2022-04-26 | 2022-05-11 | 2022-05-24 | 2022-06-08 | 2022-06-22 | 2022-07-05 | 2022-07-26 | 2022-08-23
Sand smelt | 849 | 0 | 5861 | 33318 | 12788 | 3439 | 16651 | 0 | 0
Goby family* | 10192 | 60617 | 220213 | 722469 | 660402 | 245868 | 242273 | 91242 | 80136
Indeterminate* | 7644 | 0 | 18421 | 35948 | 59372 | 9456 | 34967 | 2511 | 21088
Corkwing wrasse | 0 | 0 | 0 | 0 | 1827 | 860 | 1665 | 0 | 0
Blenny family* | 849 | 4210 | 10048 | 4384 | 5481 | 7737 | 1665 | 1674 | 844
Herring | 0 | 1684 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid family* | 0 | 0 | 0 | 0 | 0 | 0 | 833 | 0 | 0
15-spined stickleback | 0 | 842 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Two spotted clingfish | 0 | 0 | 0 | 3507 | 913 | 0 | 0 | 0 | 0
greater pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 837 | 0
snake pipefish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 844
Sole | 0 | 0 | 2512 | 0 | 0 | 0 | 0 | 0 | 844
eggs | 112966 | 123760 | 155740 | 4384 | 0 | 9456 | 0 | 0 | 0

## Metadata_22
Survey Number | Survey Date | Sample time | Net operatives | Sampling staff | Station flow (m3/Sec) | Spring/Neap | Weather Obs | Comments
1 | 2022-01-17 | 08:00-08:00 | AS, AM | KT, PA | MCW Total Flow in last 24 hours (Unit 11 flow meter failure.): 08:00 - 11:30 flow fluctuates around 38m3/s 11:30 - 12:15 flow decreased to 33m3/s 12:15 - 16:30 steady increase to 35m3/s 16:30 - 01:00 steady decrease to 34m3/s 01:00 - 08:00 general increase to 36m3/s for rest of period | Spring -3 | Wind speed (mph) 8:00 5mph General increase through the period from 5mph to 12mph by end. Wind direction 8:00 SW SW for period. Cloud (%) 8:00 0 Rainfall (mm) 8:00 0 Temperature (day) 8:00 6°C Increase from 6°C to highs of 11°C by 15:00. Decrease to 7°C by 00:00. Temperature (night) 0:00 7°C Increase to 7°C by 08:00.
2 | 2022-01-18 | 08:00-08:00 | AS, AM | OMR AW | MCW Total Flow in last 24 hours (Unit 11 flow meter failure.): 08:00 - 11:30 flow fluctuates around 38m3/s 11:30 - 12:15 flow decreased to 33m3/s 12:15 - 16:30 steady increase to 35m3/s 16:30 - 01:00 steady decrease to 34m3/s 01:00 - 08:00 general increase to 36m3/s for rest of period | Spring -2 | Wind speed (mph) 8:00 12mph Decrease from 12mph to 6mph by 18:00. General increase to 19mph by end of period. Wind direction 8:00 W Predominantly W, change to NW by 06:00. Cloud (%) 8:00 15 Rainfall (mm) 8:00 0 Temperature (day) 8:00 7°C Increased from 7°C to 10°C high by 15:00. Decrease to 8°C by 00:00. Temperature (night) 0:00 8°C Warmed from 8°C to 10°C by 08:00.
3 | 2022-01-25 | 08:00-08:00 | AS, AM | AW, PA | Drumscreen Maintenance Unit 51 flow meter failure and reinstatement MCW Total Flow in last 24 hours: 08:00 - 16:30 decrease in flow from 39m3/s to 34m3/s 16:30 - 18:00 increase to 39m3/s 18:00 - 08:00 flow fluctuates around 39m3/s | Neap -1 | Wind speed (mph) 8:00 7mph Fluctuating around 7mph for the whole period. Wind direction 8:00 SE SE changing to S by 00:00. Cloud (%) 8:00 70% Rainfall (mm) 8:00 0.1mm Temperature (day) 8:00 8°C Increase from 8°C to highs of 10°C by 15:00. Decrease to 5°C by 00:00. Temperature (night) 0:00 5°C Decrease to lows of 4°C by 03:00. Increase to 5°C by end of period.
4 | 2022-02-14 | 08:00-08:00 | AS, AM | AW, PA | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 13:30 flow increase from 37m3/s to 38.5 m3/s 13:30 - 20:00 flow fluctuates arouns 38.5m3/s 20:00 - 02:00 flow increase to 39m3/s 02:00 - 08:00 decrease to 38m3/s | Neap +3 | Wind speed (mph) 8:00 21mph Decrease from 21mph to 13mph by 21:00. Increase to 29mph by 08:00. Wind direction 8:00 NE NE until 21:00 switch to NW for rest of period. Cloud (%) 8:00 95% Rainfall (mm) 8:00 0.2mm Temperature (day) 8:00 7°C Decrease from 7°C to 6°C by 21:00. Temperature (night) 0:00 7°C Increase from 7°C to 9°C by end of period.
5 | 2022-02-15 | 08:00-08:00 | AS, AM | AW, PA | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 00:00 flow fluctuates around 38m3/s 00:00 - 00:15 flow drops to 8m3/s 00:15 - 05:15 flow fluctuates around 8m3/s 05:15 - 08:00 flow steps up to 38m3/s | Neap +4 | Wind speed (mph) 8:00 29mph Decreases to 13mph by 18:00. Increase to 41mph by 22:00. Decreasing to 31mph by 08:00. Wind direction 8:00 NW Cloud (%) 8:00 100% Rainfall (mm) 8:00 2.1mm Temperature (day) 8:00 9°C Increase to 11°C by 12:00. Temperature (night) 0:00 7°C Fluctuates around 7°C for remainder of period.
6 | 21/02/2022 | 08:00-08:00 | AS, AM | OMR, AC | Drumscreen Maintenance U31 flow meter intermittent failure throughout period MCW Total Flow in last 24 hours: 08:00 - 13:00 flow fluctuations around 38m3/s 13:00 - 14:00 flow unstable dropping to 30m3/s and returning to 38m3/s 14:00 - 15:00 flow stable around 38m3/s 15:00 - 16:00 flow issues due to U31 flow meter 16:00 - 08:00 flow stable around 38m3/s | Spring +2 | Wind speed (mph) 8:00 37mph General decrease to 15mph by 21:00. Increasing overight to 23mph by 08:00. Wind direction 8:00 NE NE switching to NW by 00:00 until end of time period. Cloud (%) 8:00 97% Rainfall (mm) 8:00 0.1mm Temperature (day) 8:00 7°C Increase to 10°C by 15:00. Temperature (night) 0:00 9°C Fluctuates around 9°C for remainder of period.
7 | 2022-03-08 | 08:00-08:00 | AS, AM | OMR, AC | Drumscreen Maintenance U31&U41 MCW flow meter intermittent failure MCW Total Flow in last 24 hours: 08:00 - 10:30 stable flow 38m3/s 10:30 - 11:00 decrease to 25m3/s 11:00 - 13:30 stable flow 26m3/s 13:30 - 14:40 increase to 36m3/s 14:40 - 23:30 flow stable at 37m3/s 23:30 - 00:30 decrease to 8m3/s 00:30 - 03:50 stable 8m3/s 03:50 - 05:30 increase to 38m3/s 05:30 - 08:00 38m3/s for rest of period | Neap -4 | Wind speed around 28mph at 08:00, general decrease to 21mph by 21:00. Increasing again to 34 mph by 08:00 Wind Direction: 08:00 - SW, change from SW to W by 15:00. 08:00 - 100% cloud cover. Day Temperature - 8°C, fluctuating around this. Night Temperature 00:00 - 8°C.
8 | 2022-03-14 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31&U41 MCW flow meter intermittent failure MCW Total Flow in last 24 hours: 08:00 - 12:40 General increase from 37m3/s to 39m3/s 12:40 - 21:00 decrease to 38m3/s 21:00 - 01:00 flow increase to 39m3/s 01:00 - 08:00 flow fluctuates around 38m3/s | Neap +2 | Wind speed fluctuating around 8mph. NE changing to S by 21:00 until end of period. Increase to 12°C by 15:00 Drops to 5°C at 00:00, general increase to 7°C by end of period.
9 | 2022-03-15 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31&U41 MCW flow meter intermittent failure MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/s | Neap +3 | Wind speed fluctuates around 8mph at 08:00 Wind Direction: 08:00 - S for most of period, change to E by end of period. 08:00 - 25% cloud cover. Day Temperature 08:00 - 7°C; increased to 9°C by 12:00. Night Temperature 00:00 - 8°C; increased to 9°C by end of period.
10 | 2022-04-04 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31&U41 MCW flow meter intermittent failure MCW Total Flow in last 24 hours: 08:00 - 23:30 Flow fluctuating aroun 37m3/s 23:30 - 00:00 Flow decrease to 8m3/s 00:00 - 04:00 Flow fluctuating around 8m3/s 04:00 - 08:00 Flow increasing to 38m3/s | Spring +2 | Wind speed around 19mph at 08:00, fluctuating around 19mph for whole period. Wind Direction: 08:00 - N for whole period. 08:00 - 100% cloud cover. Rain: 1.2mm. Temperature 08:00 - 10°C, fluctuating around this. Night Temperature 00:00 - 9°C increasing back to 10°C at 08:00.
11 | 2022-04-26 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/s for the whole period | Neap +1 | Wind speed around 16mph at 08:00, decfreasing from 16mph to 7mph by 18:00. Increases overnight to 24mph by end of period. Wind Direction: 08:00 - S for whole period. 08:00 - 30% cloud cover. No rain. Temperature 08:00 - 10°C, increasing to 12°C by 15:00. Night Temperature 00:00 - 7°C fluctuating around this for rest of period.
12 | 2020-04-27 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 00:00 Flow fluctuates around 38m3/s 00:00 - 00:15 Flow drops to 30m3/s 00:15 - 06:00 Flow increases to 38m3/s 06:00 - 08:00 Flow stable around 38m3/s | Neap +2 | Wind speed around 13mph at 08:00, increasing to 18mph by 21:00. Decrease to 13mph by end of period. Wind Direction: 08:00 - S for whole period. 08:00 - 30% cloud cover. No rain. Temperature 08:00 - 8°C, increasing to 12°C until 18:00. Night Temperature 00:00 - 6°C fluctuating around this until end of period.
13 | 2022-05-10 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 13:00 flow increases 30m3/s to 35m3/s 13:00 - 23:00 flow fluctuates around 38m3/s 23:00 - 03:00 flow decreases to 8m3/s 03:00 - 08:00 flow increases back to 38m3/s | Neap | Wind speed around 13mph at 08:00, general increase to 19mph by midday, general decrease to 16mph by end of period. Wind Direction: 08:00 - NW for whole period. 08:00 - 86% cloud cover. Rain: 0.2mm. Temperature 08:00 - 13°C, fluctuating around 13°C during daytime. Night Temperature 00:00 - 12°C for remaining period
14 | 2022-05-11 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/s for whole period. | Neap+1 | Wind speed around 18mph at 08:00, general decrease to 9mph by 08:00. Wind Direction: 08:00 - NW for whole period. 08:00 - 76% cloud cover. Rain: 0.1mm. Temperature 08:00 - 12°C, increases to 14°C by 18:00. Night Temperature 00:00 - decreases to 10°C overnight until 08:00.
15 | 23/05/2022 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/s for whole period | Neap -1 | Wind speed around 10mph at 08:00. Steady Increase to 18mph by 18:00. General decrease to 11mph overnight. Wind Direction: 08:00 - N for whole period. 08:00 - 100% cloud cover. Rain: 0.9mm. Temperature 08:00 - 12°C, fluctuates around this during the day. Night Temperature 00:00 - decreases to 9°C overnight before increasing back to 12°C by 08:00.
16 | 24/05/2022 | 08:00-08:00 | AS, AM |  | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/s for whole period. | Neap +1 | Wind speed around 11mph at 08:00. Steady Increase to 22mph by 03:00. remaining until 08:00. Wind Direction: 08:00 - NE for whole period. 08:00 - 11% cloud cover. No rain. Temperature 08:00 - 12°C, fluctuates around this during the day. Night Temperature 00:00 - decreases to 11°C until 08:00.
17 | 2022-06-07 | 08:00-08:00 | AS, AM | PA, AC | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/ | Neap | Wind speed (mph) 8:00 7mph Steady increase to 33mph by 08:00. Wind direction 8:00 W Change to N by 06:00. Cloud (%) 8:00 18%Rainfall (mm) 8:00 0.0mmTemperature (day) 8:00 15°C Temperature fluctuates around 15°C Temperature (night) 0:00 15°C Temperature fluctuates around 15°C
18 | 2022-06-08 | 08:00-08:00 | AS, AM | PA, AC | Drumscreen Maintenance U31 and U41 MCW Flow meter intermittent failure. MCW Total Flow in last 24 hours: 08:00 - 08:00 flow fluctuates around 38m3/ | Neap +1 | Wind speed (mph) 8:00 18mph Wind speed gradually drops to 9mph by 08:00. Wind direction 8:00 N Cloud (%) 8:00 75% Rainfall (mm) 8:00 0.1mm Temperature (day) 8:00 14°C Temperature increases to 16°C by 15:00. Temperature (night) 0:00 12°C Temperature increases to 15°C by 08:00.
19 | 2022-06-21 | 08:00-08:00 | AS, AM | PA, AC | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 08:00 Flow Fluctautes around 38m3/s for whole period. | Neap -2 | Wind speed around 4mph at 08:00. Steady Increase to 11mph by 21:00. Decreasing to 4pmh until 08:00. Wind Direction: 08:00 - NW moving to E by 18:00. 08:00 - 91% cloud cover. No rain. Temperature 08:00 - 15°C, increases to 17°C by 12:00. General decrease to 14°C by 21:00. Night temperature is 12 °C at 00:00, increasing to 17°C until 08:00
20 | 2022-06-22 | 08:00-08:00 | AS, AM | PA, AC | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 08:00 Flow fluctuates around 38m3/s for whole period. | Neap -1 | Wind speed around 4mph at 08:00. Steady Increase to 9mph by 21:00. Decreasing to 5pmh until 08:00. Wind Direction: 08:00 - E for the whole period. 08:00 - 11% cloud cover. No rain. Temperature 08:00 - 17°C, increases to 21°C by 15:00. Night temperature is 14 °C at 00:00, increasing to 17°C until 08:00.
21 | 2022-07-04 | 08:00-08:00 | AS, AM | OMR, PA | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 00:10 Flow fluctuating around 38m3/s 00:10 - 04:00 flow decreases to 30m3/s 04:00 - 08:00 Flow inc | Neap -3 | Wind speed (mph) 8:00 13mph Increase to 15mph by 12:00. General decrease to 8mph by the end of the period. Wind direction 8:00 N Move to NE overnight. Cloud (%) 8:00 34% Rainfall (mm) 8:00 0.0mm Temperature (day) 8:00 14°C General increase to 17°C by 15:00. Temperature (night) 0:00 12°C Increasing to 13°C by 08:00
22 | 2022-07-05 | 08:00-08:00 | AS, AM | OMR, PA | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 00:00 Flow fluctuates around 38m3/s 00:00 - 08:00 Flow decrease | Neap -2 | Wind speed (mph) 8:00 8mph Wind direction 8:00 E Cloud (%) 8:00 11% Rainfall (mm) 8:00 0.0mm Temperature (day) 8:00 13°C Temperature (night) 0:00 14°C
23 | 2022-07-25 | 08:00-08:00 | AS, AM | PA, AC | Drumscreen Maintenance MCW Total Flow in last 24 hours: 08:00 - 08:00 Flow fluctuates around 38m3/s | Neap +2 | Wind speed around 19mph at 08:00. Decrease to 11mph by 18:00. Fluctuates around 11pmh till 08:00. Wind Direction: 08:00 - NE. Changes to E by 21:00 and remains till 08:00. 08:00 - 80% cloud cover. 0.5mm of rainfall. Temperature 08:00 - 16°C, increases to 18°C by 12:00. Night temperature is 14 °C at 00:00, increasing to 15°C until 08:00.
24 | 2022-07-26 | 08:00-08:00 | AS, AM | PA, AC | Drum screen maintenance MCW Total Flow in last 24 hours: 08:00 - 08:00 fluctuates around 39m3/s | Neap +3 | Wind speed around 11mph at 08:00. Increase to 13mph by 12:00. General decrease to 8pmh till 08:00. Wind Direction: 08:00 - E. Changes to S by 06:00 and remains till 08:00. 08:00 - 13% cloud cover. No rainfall. Temperature 08:00 - 15°C, increases to 21°C by 15:00. Night temperature is 12 °C at 00:00, increasing to 16°C until 08:00.
25 | 2022-08-01 | 08:00-08:00 | AS, AM | KT, AC | Drum screen maintenance MCW Total Flow in last 24 hours: 08:00-08:00 fluctuates arund 38.5 m3/s | Spring +2 | Wind speed around 13mph at 08:00. Increase to 16mph by 15:00. Increases to 19pmh till 08:00. Wind Direction: 08:00 - NW. 08:00 - 100% cloud cover. 0.6mm rainfall. Temperature 08:00 - 18°C, increases to 21°C by 15:00. Night temperature is 18 °C at 00:00.
26 | 2022-08-22 | 08:00-08:00 | AS, AM | OMR, PA | Drum screen 3 out of service MCW Total Flow in last 24 hours: 08:00 -10:00 Flow fluctuates around 37m3/hr 10:00-08:00 Flow fluctuates around 38.5m3/hr |  | Wind speed around 12mph at 08:00. Increase to 19mph by 15:00. The decreased back down to 14 mph by 08:00. Wind Direction: 08:00 - NW. 08:00 - 70% cloud cover. 0.25mm rainfall. Temperature 08:00 - 17°C, increases to 20°C by 18:00. Night temperature increased from 17°C to 18°C by 08:00.
27 | 2022-08-23 | 08:00-08:00 | AS, AM | OMR, PA | Drum screen 3 out of service MCW Total Flow in last 24 hours: Flow fluctuated around 38.5 m3/hr |  | Wind speed gradually increased to 21mph by 15:00. Dropped back to 13 mph by 08:00. Wind Direction: 08:00 - W, then NW by 12:00. Then fluctuated btween N and W until 08:00. 08:00 - 75% cloud cover. 1.1mm rainfall. Temperature 08:00 - 18°C, no change by 18:00. Night temperature 18°C, no change by 08:00.
28 | 2022-09-05 | 08:00-08:00 | AS, AM | PA, AC | Drum screen out of service MCW Total Flow in last 24 hours: Fluctuated around 38m3/s |  | Wind speed 20mph at 08:00 then decreases to 19mph at 21:00. Increases back to 22mph by 00:00 and then drops to 17mph by 08:00. Wind Direction: 08:00 - SW, then Fluctuates between SW and W between 08:00 and 08:00. - 80% cloud cover. 0.1mm rainfall. Temperature 08:00 - 17°C, Fluctuates from 16°C to 18°C bewtween 08:00 and 00:00. Night temperature 16°C at 00:00, increases to 17°C by 08:00.
29 | 2022-09-06 | 08:00-08:00 | AS, AM | PA, AC | Drum screen out of service MCW Total Flow in last 24 hours: From 08:00 to 14:30 the flow gradually increase from 38 to 39.5m3/s. At around 14:30 the flow dropped back to 38m3/s and fluctuated around this point until 08:00. |  | Wind speed 17mph at 08:00 then Increased to 21mph by 21:00. Stays at 21mph until 08:00. Wind Direction: 08:00 - W, no change by 08:00. - 82% cloud cover, 1mm rainfall. Temperature 08:00 - 17°C,Fluctuates bteween 16°C and 17°C bewtween 08:00 and 00:00. Night temperature 16°C at 00:00, no change by 08:00.
30 | 2022-09-26 | 08:00-08:00 | AS, AM | KC, AC | Drum screen 2 out of service and maintenance on drumscreen 3. MCW Total Flow in last 24 hours: Stayed at 30m/s from 08:00 - 12:40 Fluctuated around 38m/s from 12:40 - 08:00. |  | Wind speed 24mph at 08:00 then Increased to 30mph by 15:00. Decreased gradually to 20mph by 08:00. Wind Direction: 08:00 - NE, no change by 08:00. - 70% cloud cover, 3mm rainfall. Temperature 08:00 - 14°C, Decreased to 13°C by 21:00. Night temperature 12°C at 00:00, no change by 08:00.
31 | 2022-10-10 | 08:00-08:00 | AS, AM | KT, PA | Drum screen 2 and 3 failure MCW Total Flow in last 24 hours: Between 08:00 and 20:00 the flow fluctuated between 30m3/s and 32m3/s. Between 20:00 and 23:30 the flow fluctuated around 38m3/s. Between 23:30 and 04:00 the flow fluctuated between 36m3/s and 37m3/s. Between 04:00 and 08:00 the flow fluctuated around 38m3/s and 39m3/s. |  | Wind speed 16mph at 08:00 then Gradually dropped to 4mph by 03:00. Then increased to 8mph by 08:00. Wind Direction: 08:00 - NE, no change by 08:00. - 0% cloud cover, 0mm rainfall. Temperature 08:00 - 11°C,Increases to 16°C by 12:00. Drops to 11°C by 21:00. Night temperature 11°C at 00:00, no change by 08:00.
32 | 2022-10-11 | 08:00-08:00 | AS, AM | KT, PA | Drum screen 2 and 3 failure MCW Total Flow in last 24 hours: Fluctuated around 38.5m3/s between 08:00 and 11:00. Gradually decreased from 39m3/s to 36m3/s between 11:00 to 14:00. Increased back to 39m3/s by 17:00. Fluctuated between 38m3/s and 39m3/s between 17:00 and 00:00. Decreased from 39m3/s to 36m3/s between 00:00 and 03:00, Increased back to 39m3/s by 05:30. Fluctuated around 38m3/s and 39m3/s by 08:00. |  | Wind speed 7mph at 08:00 then Gradually increased to 16mph by 08:00. Wind Direction: 08:00 - SW, no change by 08:00. - 63% cloud cover, 0mm rainfall. Temperature 08:00 - 12°C,Increases to 14°C by 12:00. Drops to 12°C by 21:00. Night temperature 12°C at 00:00, Increased to 13°C by 08:00.
33 | 2022-10-24 | 08:00-08:00 | AS, AM | PA, AC | Drum screen maintenance MCW Total Flow in last 24 hours: Fluctuated around 38m3/s between 08:00 and 08:00. |  | Wind speed 13mph at 08:00 then Gradually increased to 22mph by 21:00. Then dropped back to 14mph by 08:00. Wind Direction: 08:00 - NW, no change by 08:00. - 68% cloud cover, 0.2mm rainfall. Temperature 08:00 - 13°C, Increases to 15°C by 15:00. Drops to 14°C by 21:00. Night temperature 13°C at 00:00, no change by 08:00.
34 | 2022-11-01 | 08:00-08:00 | AS, AM | OMR, KT, AW | Drum screen maintenance MCW Total Flow in last 24 hours: Between 08:00 and 13:15 the flow fluctuated around 25m3/s. Between 13:15 and 14:00 the flow fluctuated around 29m3/s. Between 14:00 and 22:00 the flow fluctuated around 33m3/s. Between 22:00 and 05:30 the flow fluctuated around 24m3/s. Between 05:30 and 07:00 the flow fluctuated around 28m3/s. Between 07:00 and 08:00 the flow fluctuated around 32m3/s. |  | Wind speed 23mph at 08:00 then Drops to 15mph by 12:00 and then increases to 33mph by 08:00. Wind Direction: 08:00 - NW, no change by 08:00. - 85% cloud cover, 1.5mm rainfall. Temperature 08:00 - 13°C, Drops to 11°C by 21:00. Night temperature 11°C at 00:00, Increases to 13°C by 08:00.
35 | 2022-11-02 | 08:00-08:00 | AS, AM | OMR, KT, AW | Drum screen maintenace. MCW Total Flow in last 24 hours: Between 08:00 and 21:00 the flow fluctuated between 32m3/s and 34m3/s. Between 21:00 and 04:20 the flow fluctuated around 24m3/s. Between 04:20 and 05:45 the flow fluctuated increased from 24m3/s to 38m3/s. Between 05:45 and 08:00 the flow fluctuated around 38m3/s. |  | Wind speed 29mph at 08:00 then Increased to 43mph by 15:00. Dropped to 24mph by 18:00, increased to 29mph by 21:00. Dropped to 14mph by 08:00. Wind Direction: 08:00 - NW, no change by 08:00. - 67% cloud cover, 0.8mm rainfall. Temperature 08:00 - 12°C Increases to 14°C by 15:00. Drops to 12°C by 21:00. Night temperature 12°C at 00:00, Dropped to 11°C by 08:00.
36 | 2022-11-07 | 08:00-08:00 | AS, AM | AW, PA | Drum screen maintenance. MCW Total Flow in last 24 hours: Between 08:00 and 22:00 the flow fluctuated between 38m3/s and 39m3/s. Between 22:00 and 05:45 the flow fluctuated around 16m3/s. Between 05:45 and 08:00 the flow fluctuated between 38m3/s and 39m3/s. |  | Wind speed 27mph at 08:00 then Increased to 39mph by 18:00. Dropped to 21mph by 21:00. Gradually increased to 32mph by 08:00. Wind Direction: 08:00 - NW, no change by 08:00. - 100% cloud cover, 1.3mm rainfall. Temperature 08:00 - 13°C Increases to 14°C by 12:00. Drops to 12°C by 21:00. Night temperature 13°C at 00:00,Dropped to 12°C by 08:00.
37 | 2022-11-14 | 08:00-08:00 | AS, AM | OMR, KT, AW | Drum screen maintenace. MCW Total Flow in last 24 hours: Between 14:00 and 23:00 the flow fluctuated between 38m3/s and 39m3/s. Between 23:00 and 00:15 the flow dropped to 4m3/s, remained here for 4.5 hours and then gradually increased back to 38m3/s by 07:30. . Between 07:30 and 14:00 the flow fluctuated between 38m3/s and 39m3/s. |  | Wind speed 21mph at 14:00 thenIncreased to 36mph by 03:00. Dropped to 15mph by 12:00. Gradually increased to 21mph by 14:00. Wind Direction: 14:00 - NW, Fluctuated betweem NW and SW. - 0% cloud cover,0mm rainfall. Temperature 14:00 - 13°C Drops to 12°C by 21:00. Night temperature 12°C at 02:00, Dropped to 11°C by 14:00.
38 | 2022-12-05 | 08:00-08:00 | AS, AM | OMR, KT, AW | MCW Total Flow in last 24 hours: Between 08:00 and 08:00 the flow fluctuated between 37.7m3/s and 39.3 m3/s |  | Wind speed 19mph at 08:00 then Decreased to 11mph by 08:00. Wind Direction: 08:00 - SE, no change by 08:00. - 85% cloud cover, 0.1mm rainfall. Temperature 08:00 - 6°C Increases to 8°C by 12:00. Drops to 7°C by 21:00. Night temperature 7°C at 00:00, no change by 08:00.
39 | 2022-12-06 | 08:00-08:00 | AS, AM | KT, MG | Drum screen 2 and 3 failure MCW Total Flow in last 24 hours: Between 08:00 and 01:00 the flow fluctuated around 39m3/s. At 01:00 the flow dropped from 39m3/s to 22m3/s. Between 01:00 and 04:00 the flow fluctuated increased from 22m3/s to 25m3/s. Between 04:00 and 05:30 the flow increased from 25m3/s to 39m3/s. Between 05:30 and 08:00 the flow fluctuated around 39m3/s. |  | Wind speed 11mph at 08:00 then Drops to 6mph by 08:00. Wind Direction: 08:00 - SE, no change by 08:00. - 100% cloud cover, 0mm rainfall. Temperature 08:00 - 7°CDecreases to 4°C by 21:00. Night temperature 3°C at 00:00, no change by 08:00.
40 | 2022-12-12 | 08:00-08:00 | AS, AM | AC, PA | Drum screen 3 maintenance MCW Total Flow in last 24 hours: Between 08:00 and 08:00 flow fluctuated between 37.8m3/s and 39.3m3/s. |  | Wind speed 9mph at 08:00 Increased to 20mph by 21:00. Drops to 13mph by 00:00. Increases back to 18mph by 08:00. Wind Direction: 08:00 - SW, no change by 08:00. - 0% cloud cover, 0mm rainfall. Temperature 08:00 - 1°C Increases to 3°C by 21:00. Night temperature 5°C at 00:00, Increases to 5°C by 08:00.

## Total abundance_22
MAIN CATCH ABUNDANCE + TRASH ABUNDANCE | 17-18/01/2022 | 18-19/01/2022 | 24-25/01/2022 | 14-15/02/2022 | 15-16/02/2022 | 21-22/02/2022 | 08-09/03/2022 | 14-15/03/2022 | 15-16/03/2022 | 4-5/04/2022 | 26-27/04/2022 | 27-28/04/2022 | 10-11/05/2022 | 11-12/05/2022 | 23-24/05/2022 | 24-25/05/2022 | 7-8/06/2022 | 8-9/06/2022 | 21-22/06/2022 | 22-23/06/2022 | 4-5/07/2022 | 5-6/07/2022 | 25-26/07/2022 | 26-27/07/2022 | 1-2/08/2022 | 22-23/08/2022 | 23-24/08/2022 | 5-6/09/2022 | 6-7/09/2022 | 26-27/09/2022 | 10-11/10/2022 | 11-12/10/2022 | 24-25/10/2022 | 01-02/11/2022 | 02-03/11/2022 | 07-08/11/2022 | 14-15/11/2022 | 05-06/12/2022 | 06-07/12/2022 | 12-13/12/2022
Species (cells linked to species list) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Pogge | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 53 | 35 | 47 | 81 | 59 | 1204 | 432 | 107 | 90 | 151 | 24 | 9 | 21 | 4 | 10 | 3 | 0 | 2 | 3 | 1 | 0 | 0 | 4 | 4 | 2 | 8 | 13 | 12 | 8 | 2935.4 | 635.3333 | 15 | 23 | 16 | 28 | 59 | 36 | 186 | 784 | 177
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 4 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 1 | 0 | 0 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.3333 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 6
Herring | 5 | 3 | 2 | 2 | 0 | 36 | 8 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 0
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4
Sprat | 57 | 25 | 20 | 1 | 6 | 240 | 90 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.8 | 3.3333 | 0 | 0 | 0 | 0 | 0 | 366 | 2414 | 2290 | 284
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 1 | 0 | 1 | 3 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 0 | 1 | 0 | 1 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Bib | 2 | 0 | 0 | 4 | 5 | 19 | 6 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0 | 0 | 1
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 3 | 0 | 0 | 2 | 1 | 8 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Poor cod | 4 | 0 | 3 | 2 | 3 | 19 | 6 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 1 | 3 | 1 | 1
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 0 | 0 | 0 | 0 | 16 | 2 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 1 | 2 | 0 | 0 | 12 | 2 | 0 | 1 | 6 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 8.8 | 6.3333 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 3 | 0
Black goby | 1 | 0 | 0 | 0 | 0 | 4 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Common goby | 0 | 0 | 0 | 2 | 0 | 54 | 12 | 5 | 2 | 3 | 0 | 1 | 0 | 0 | 7 | 2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 61.1 | 2 | 2 | 4 | 1 | 8 | 3 | 0 | 7 | 5 | 0
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 1 | 0 | 0 | 5 | 2 | 95 | 1 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 10 | 1 | 6 | 0 | 2 | 0 | 10 | 1 | 0 | 2
Rock goby | 1 | 1 | 1 | 12 | 0 | 8 | 4 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 2 | 1 | 2 | 0 | 5 | 7 | 5 | 12 | 7 | 6 | 13 | 2 | 1 | 6 | 4 | 46.9 | 27 | 64 | 9 | 9 | 2 | 30 | 4 | 5 | 4 | 6
Sand goby | 18 | 13 | 11 | 35 | 22 | 1205 | 10 | 5 | 17 | 2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 3 | 2 | 4 | 2 | 4 | 2 | 5 | 46.8 | 1 | 45 | 2 | 4 | 7 | 4 | 2 | 0 | 2 | 2
Transparent goby | 1 | 0 | 0 | 0 | 0 | 0 | 4 | 2 | 2 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11.9 | 19.3333 | 50 | 10 | 5 | 6 | 11 | 5 | 3 | 5 | 8
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 4.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 10.7 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 2 | 3 | 3 | 4 | 2 | 6 | 2 | 0 | 0 | 3 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 0 | 25.2 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 28 | 56 | 1
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.8 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 4 | 1 | 0 | 5 | 1 | 7 | 4 | 1 | 2 | 3 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 5 | 4 | 1
Mullet indet | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 22.4 | 35 | 16 | 3 | 0 | 0 | 0 | 0 | 9 | 2 | 1
Thin lipped grey mullet | 0 | 0 | 2 | 0 | 0 | 0 | 3 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Dab | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flounder | 0 | 0 | 0 | 0 | 0 | 6 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Plaice | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 0 | 2 | 1 | 3 | 0 | 6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.9 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 4 | 2
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 1 | 1 | 1 | 0 | 4 | 0 | 3 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 4 | 3 | 2 | 0 | 1 | 0 | 23.5 | 57.3333 | 80 | 14 | 5 | 6 | 3 | 1 | 8 | 9 | 1
Nilsson's pipefish | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10.8 | 12 | 13 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 1 | 0 | 2 | 1 | 0 | 10 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8.7 | 7 | 19 | 14 | 2 | 2 | 0 | 0 | 4 | 0 | 4
Worm pipefish | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 2 | 0 | 0 | 0 | 0 | 2 | 4 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 1 | 0 | 0 | 1 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea bream indet | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ling | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Goby indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Total biomass_22
MAIN CATCH BIOMASS + TRASH BIOMASS | 17-18/01/2022 | 18-19/01/2022 | 24-25/01/2022 | 14-15/02/2022 | 15-16/02/2022 | 21-22/02/2022 | 08-09/03/2022 | 14-15/03/2022 | 15-16/03/2022 | 4-5/04/2022 | 26-27/04/2022 | 27-28/04/2022 | 10-11/05/2022 | 11-12/05/2022 | 23-24/05/2022 | 24-25/05/2022 | 7-8/06/2022 | 8-9/06/2022 | 21-22/06/2022 | 22-23/06/2022 | 4-5/07/2022 | 5-6/07/2022 | 25-26/07/2022 | 26-27/07/2022 | 1-2/08/2022 | 22-23/08/2022 | 23-24/08/2022 | 5-6/09/2022 | 6-7/09/2022 | 26-27/09/2022 | 10-11/10/2022 | 11-12/10/2022 | 24-25/10/2022 | 01-02/11/2022 | 02-03/11/2022 | 07-08/11/2022 | 14-15/11/2022 | 05-06/12/2022 | 06-07/12/2022 | 12-13/12/2022
Species (cells linked to species list) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Pogge | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser sandeel | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raitt's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Eel | 0 | 0 | 34 | 33 | 0 | 29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 94 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 35 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yellow eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Silver eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Glass eel | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sand smelt | 622 | 366 | 660 | 1085 | 716 | 11334 | 5224 | 1408 | 1189 | 1813 | 325 | 119 | 280 | 50 | 15 | 34 | 0 | 9 | 17 | 2 | 0 | 0 | 9 | 2 | 2 | 11 | 27 | 22 | 6 | 5057.5 | 1068.3333 | 30 | 65 | 44 | 60 | 138 | 70 | 383 | 2037 | 487
Grey triggerfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Garfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shanny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 24 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tompot blenny | 0 | 0 | 0 | 0 | 0 | 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's blenny | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (common) | 0 | 32 | 0 | 6 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (indet) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dragonet (reticulated) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Scad/Horse Mackerel | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Clupeid indet | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.3333 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 2
Herring | 20 | 11 | 6 | 83 | 0 | 369 | 112 | 0 | 0 | 70 | 0 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 9 | 0
Pilchard | 0 | 0 | 0 | 0 | 0 | 0 | 61 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5
Sprat | 39 | 17 | 15 | 1 | 5 | 268 | 109 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8.8 | 3.3333 | 0 | 0 | 0 | 0 | 0 | 372 | 1795 | 1962 | 233
Conger eel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long-spined sea scorpion | 23 | 0 | 14 | 92 | 81 | 18 | 0 | 11 | 0 | 0 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 0 | 0 | 0 | 0
Short-spined sea scorpion | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lumpsucker | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5-bearded rockling | 0 | 54 | 0 | 42 | 0 | 92 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 14 | 0
Bib | 75 | 0 | 0 | 262 | 456 | 1012 | 581 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 151 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 103 | 19 | 0 | 0 | 79
Cod | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gadoid indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pollack | 205 | 0 | 0 | 177 | 20 | 222 | 0 | 0 | 211 | 0 | 3633 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 23 | 0 | 0 | 0 | 0 | 22 | 0 | 0 | 0 | 0 | 0
Poor cod | 30 | 0 | 35 | 56 | 26 | 684 | 38 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 50 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 27 | 31 | 33 | 96 | 15 | 19
Trisopterus sp | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Whiting | 0 | 0 | 0 | 0 | 0 | 1345 | 138 | 0 | 15 | 56 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15-spined stickleback | 0 | 6 | 7 | 0 | 0 | 76 | 17 | 0 | 13 | 61 | 44 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 14.7 | 14.6667 | 5 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3-spined stickleback | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0
Black goby | 1 | 0 | 0 | 0 | 0 | 28 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0
Common goby | 0 | 0 | 0 | 1 | 0 | 26 | 6 | 5 | 2 | 2 | 0 | 1 | 0 | 0 | 4 | 4 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 25.6 | 1 | 1 | 3 | 1 | 3 | 1 | 0 | 2 | 3 | 0
Gobiidae indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lozano's goby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Painted goby | 1 | 0 | 0 | 3 | 2 | 38 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 5.6667 | 1 | 2 | 0 | 1 | 0 | 3 | 1 | 0 | 2
Rock goby | 21 | 1 | 24 | 26 | 0 | 16 | 7 | 3 | 5 | 6 | 0 | 1 | 14 | 0 | 26 | 4 | 2 | 0 | 17 | 23 | 30 | 47 | 45 | 28 | 530 | 13 | 46 | 11 | 18 | 112.6 | 41.3333 | 165 | 36 | 107 | 9 | 95 | 27 | 14 | 13 | 61
Sand goby | 48 | 25 | 32 | 64 | 49 | 2138 | 27 | 7 | 36 | 2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 1 | 2 | 2 | 1 | 1 | 1 | 3 | 33.3 | 1 | 105 | 2 | 3 | 5 | 2 | 1 | 0 | 3 | 3
Transparent goby | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 2 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.9 | 3.3333 | 13 | 2 | 1 | 1 | 3 | 2 | 2 | 3 | 2
Two-spotted goby | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ballan wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 24.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corkwing wrasse | 0 | 0 | 0 | 0 | 0 | 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 1 | 0 | 148 | 0 | 21.3 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Goldsinny wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Wrasse indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baillon's wrasse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Montagu's sea snail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bass | 9 | 17 | 14 | 23 | 73 | 99 | 14 | 0 | 0 | 35 | 0 | 7 | 6 | 7 | 0 | 0 | 98 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 111 | 0 | 1388.8 | 206 | 0 | 12 | 0 | 0 | 0 | 0 | 193 | 356 | 4
Striped red mullet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 207.2 | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Golden grey mullet | 28 | 5 | 0 | 47 | 7 | 122 | 109 | 10 | 24 | 192 | 23 | 45 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 95 | 6 | 1 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 98 | 92 | 1
Mullet indet | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 6.8 | 6.6667 | 5 | 3 | 0 | 0 | 0 | 0 | 3 | 2 | 1
Thin lipped grey mullet | 0 | 0 | 13 | 0 | 0 | 0 | 44 | 0 | 77 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea lamprey | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Butterfish | 0 | 0 | 3 | 7 | 1 | 10 | 8 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 14 | 4 | 0
Dab | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flounder | 0 | 0 | 0 | 0 | 0 | 56 | 103 | 64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 86 | 0 | 0 | 0 | 0
Plaice | 0 | 131 | 47 | 0 | 0 | 0 | 66 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thornback ray | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Salmonid | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea Trout | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mackerel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Brill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lesser spotted dogfish | 0 | 1201 | 608 | 1344 | 0 | 3681 | 0 | 599 | 730 | 525 | 561 | 471 | 0 | 0 | 0 | 0 | 454 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2323.7 | 0 | 0 | 0 | 0 | 0 | 785 | 671 | 508 | 2729 | 1216
Dover sole | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 36 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solenette | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gilt-head sea bream | 0 | 0 | 0 | 0 | 0 | 41 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater pipefish | 0 | 1 | 1 | 42 | 0 | 4 | 0 | 43 | 0 | 0 | 0 | 23 | 0 | 33 | 0 | 1 | 0 | 18 | 0 | 0 | 0 | 2 | 1 | 5 | 7 | 31 | 0 | 1 | 0 | 4.9 | 7.6667 | 64 | 2 | 3 | 2 | 1 | 1 | 5 | 62 | 14
Nilsson's pipefish | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.9 | 3.3333 | 5 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Pipefish indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Snake pipefish | 1 | 0 | 5 | 1 | 0 | 32 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 29 | 2.3333 | 19 | 11 | 4 | 1 | 0 | 0 | 2 | 0 | 2
Worm pipefish | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 7 | 4 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Lesser weever | 0 | 0 | 0 | 0 | 0 | 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Grey gurnard | 0 | 12 | 0 | 0 | 37 | 69 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 51 | 0
Tub gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
John dory | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2-spotted clingfish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spiny seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Haddock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thick lipped mullet | 0 | 0 | 0 | 0 | 0 | 114 | 0 | 18 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gurnard | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Starry smooth hound | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Greater sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Corbin's sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Smooth sandeel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short-snouted seahorse | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0
Tadpole fish | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sea bream indet | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ling | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Goby indet | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0