## control (hidden)
but your chains
Click here to name and save
new spreadsheet in to
the current active directory

## Introduction
Groundwater risk assessment for treated effluent discharges to infiltration systems
Infiltration Worksheet , Release v3.0
Date of Workbook Issue: March 2022
This worksheet has been produced in combination with the document: H1 Annex J5 User Manual version 2.0 (Environment Agency, 2014).
© Environment Agency, 2021
All rights reserved. You will not modify, reverse compile or otherwise dis-assemble the worksheet.
Liability: The Environment Agency does not promise that the worksheet will provide any particular facilities or functions. You must ensure that the worksheet meets your needs and you remain solely responsible for the competent use of the worksheet. You are entirely responsible for the consequences of any use of the worksheet and the Agency provides no warranty about the fitness for purpose or performance of any part of the worksheet. We do not promise that the media will always be free from defects, computer viruses, software locks or other similar code or that the operation of the worksheet will be uninterrupted or error free. You should carry out all necessary virus checks prior to installing on your computing system.
IMPORTANT: To enable MS Excel worksheet, click the Microsoft Office Button click Excel Options, click Add-Ins. In the Manage box, select Excel Add-ins. Click Go. Select Analysis ToolPak and Analysis ToolPak-VBA (to calculate error functions)
Details to be completed for each assessment
Site Name: | Pen y Glol Caravan Park
Site Address: | Pen y Glol Caravan Park, Lloc, HOLYWELL, Flintshire, CH8 8RQ
Completed by: | Nick Rukin (Rukhydro Ltd)
Date: | 2024-07-08 |  | Version: | 1.NO3 likely
Substance | Nitrate
Environmental Standard (CT) | 50 | mg/l | Origin of CT: | DWS as mg/l NO3
This spreadsheet has been developed as a tool to assist groundwater risk assessment for effluent discharges to infiltration systems. The following worksheets are available:
Infiltration System
Attenuation_unsatzone
Dilution
Attenuation_satzone
Summary
Simple calcs
Site details entered on this page are automatically copied to each worksheet.
The worksheet uses the following colour coding:
Worksheet option with pull down menu
Data entry
Data origin / justification should be noted in cells coloured yellow and fully documented in subsequent reports.
Data carried forward from an earlier worksheet
Calculation
It is recommended that a copy of the original worksheet is saved (all data fields in the original copy are blank).

## Infiltration System
Infiltration Worksheet
Infiltration System
| Substance |  | Nitrate |  | From introduction sheet |  | This sheet allows user to enter effluent concentration and details of infitration system
| Compliance value or environmental standard | CT | 50 | mg/l | From introduction sheet
Calculate for ionic organic chemicals (acids)
| Input Parameters | Variable | Value | Unit | Source of parameter value |  |  |  | Calc cells to be hidden
Standard entry
| Concentration of substance in discharge (entering infiltration system) | Ce | 243.5714 | mg/l | Two samples collected Nov 2023 and June 2024 have TIN of 50.4 and 42.2mg/l as N total inorganic nitrogen. Assume range 45-55-65mg/l N. |  |  |  | 0 | Septic tank
| Type of treatment plant | Package treatment plant | [6 empty] | 2 | Package treatment plant
[9 empty] | 0 | Treatment plant
| Water use and percolation rate (for use only with septic tanls and package treatment plants) | [7 empty] | 0 | Other
| Number of persons | p |  |  |  | Not valid for this treatment plant option |  |  | 2
| Water use |  | 180 | litres/person/day |  | Not valid for this treatment plant option
| Percolation rate | Vp |  | s/mm |  | Not valid for this treatment plant option
Specify discharge (Q1) or calculate based on use (Q2) |  | Specified discharge Q1 | [6 empty] | 1 | Specified discharge Q1 | 15
| Discharge rate | Q1 | 15 | m3/d | Assumed maximum = 15 cubic metres per day | Value calculated and not specified by user |  |  | 0 | Calculated discharge Q2
| Calculated discharge | Q2 | 0 | m3/d |  | Value specifed by user and not calculated
Area of drainage fied and hydraulic loading
Specify area of drainage field or calculate based on percolation rate |  |  | Specify | [5 empty] | 1 | Specify
| Enter area of drainage field | A | 170 | m2 | 4 No 50m long trenches each 0.8 to 0.9m wide (Rukhydro, 2021, Section 2.2.4). | Value calculated and not specified by user |  |  | 0 | Calculate
| Calculated area of drainage field | A | 0 | m2 |  | Value specifed by user and not calculated
| Calculated infiltration rate | Inf | 0.088235 | m/d
[6 empty] | Site being assessed: |  | Pen y Glol Caravan Park
[6 empty] | Completed by: |  | Nick Rukin (Rukhydro Ltd)
[6 empty] | Date: |  | 2024-07-08
[6 empty] | Version: |  | 1.NO3 likely
Note on B17: Percolation test undertaken according to BS6297

## Attenuation_unsatzone
Infiltration Worksheet
| Attenuation unsaturated zone | [7 empty] | Calc cells to be hidden
| Contaminant |  | Nitrate |  | From introduction sheet |  | This sheet calculates attenuation factor for the unsaturated zone; concentration at base of unsaturated zone and discharge consent limit
| Compliance value or environmental standard | CT | 50 | mg/l | From introduction sheet
| Concentration of substance in substance in discharge (entering infiltration system) | Ce | 243.5714 | mg/l | From infiltration sheet
| Input Parameters | Variable | Value | Unit | Source of parameter value
Standard entry
Drainage Layer
| Infiltraton rate | Inf | 0.088235 | m/d | From infiltration sheet |  |  |  | 1 | No degradation occurs
| Thickness of drainage layer | S1 | 0.3 | m | Rukhydro GWRA (RP030i1) Fig 2.3 |  |  |  | 0 | Degradation occurs - sorbed and dissolved phases
| Water filled porosity | q1 | 0.3 | fraction | LandSim manual Table 5.5 range for coarse gravel is 0.24 to 0.36. Rukhydro GWRA (RP030i1) Fig 2.3 notes 20-50mm gravel. This is coarse gravel as defined by ISO14688 (https://en.wikipedia.org/wiki/Gravel). |  |  |  | 0 | Degradation occurs dissolved phase only
| Bulk density | r1 | 1.61 | g/cm3 | Assume mineral density of 2.3g/cm3 and then calculate with porosity.
| Calculated dispersivity | D1 | 0.03 | m | calculated |  |  |  | 1e-99
| Option to select degradation | No degradation occurs
Determine remedial target based on assumed concentration | Half life for degradation of substance | t1/2 | 1e+100 | days |  | Half life not required - No degradation occuring
| Calculated decay rate | l1 | 1e-99 | days-1 | calculated (very low value set if no degradation) | Default value of 1/10^99 used |  |  | 1
[9 empty] | 1 | User specified value for partition coefficient
| Enter method of defining partition co-efficient (using pull down list) | User specified value for partition coefficient | [6 empty] | 0 | Calculate for non-polar organic chemicals
Entry if specify partition coefficient (option)
| Soil water partition coefficient | Kd1 | 0 | l/kg | No retardation assumed | Not valid - Calculated value used
Entry for organic chemicals (option)
| Fraction of organic carbon (in soil) | foc1 | 0.01 | fraction |  | Not valid - User specified value used
| Organic carbon partition coefficient | Koc1 | 10 | l/kg |  | Not valid - User specified value used
| Soil water partition coefficient used in assessment | Kd1 | 0 | l/kg | Specified value
| Retardation factor | Rfu1 | 1
| Unretarded travel time (no dispersion) | tu1 | 1.02 | d
| Unretarded travel time (with dispersion) | tu1 | 0.918 | d
| Retarded travel time (with dispersion) | tr1 | 0.918 | d
| Attenuation factor | AFu1 | 1
Unsaturated Zone
| Thickness of unsaturated zone below drainage field | S2 | 41.5 | m | Rukhydro GWRA (RP030i1) Section 3.5.4 (range 41.5 to 50.5m).
| Water filled porosity | q2 | 0.01 | fraction | Rukhydro GWRA (RP030i1) Section 3.5.4. Fracture porosity.
| Bulk density of unsaturated zone | r2 | 2.277 | g/cm3 | Assume mineral density of 2.3g/cm3 and then calculate with porosity.
| Calculated dispersivity | D2 | 4.15 | m | calculated |  |  |  | 1 | No degradation occurs
| Option to select degradation | No degradation occurs | [6 empty] | 0 | Degradation occurs - sorbed and dissolved phases
Determine remedial target based on assumed concentration | Half life for degradation of substance | t1/2 | 1e+100 | days |  | Half life not required - No degradation occuring |  |  | 0 | Degradation occurs dissolved phase only
| Calculated decay rate | l2 | 1e-99 | days-1 | calculated (very low value set if no degradation) | Calculated from half life (above)
| Fraction of rapid flow through unsaturated zone | B | 0 | fraction | Already accounted for with 1% fracture porosity |  |  |  | 1e-99
1
| Enter method of defining partition co-efficient (using pull down list) | User specified value for partition coefficient | [6 empty] | 1 | User specified value for partition coefficient
| Entry if specify partition coefficient (option) | [7 empty] | 0 | Calculate for non-polar organic chemicals
| Soil water partition coefficient | Kd2 | 0 | l/kg | No retardation assumed | Not valid - Calculated value used
Entry for organic chemicals (option)
| Fraction of organic carbon (in soil) | foc2 | 0.01 | fraction |  | Not valid - User specified value used
| Organic carbon partition coefficient | Koc2 | 10 | l/kg |  | Not valid - User specified value used
| Soil water partition coefficient used in assessment | Kd2 | 0 | l/kg | Specified value
| Retardation factor | Rfu2 | 1
| Unretarded travel time (no dispersion) | tu2 | 4.7033 | d
| Unretarded travel time (with dispersion) | tu2 | 4.233 | d
| Retarded travel time (with dispersion) | tr2 | 4.233 | d
| Attenuation factor | AFu2 | 1
| Total unretarded travel time | tu1 + tu2 | 5.7233 | d
| Total retarded travel time | tr1 + tr2 | 5.7233 | d
| Attenuation factor and discharge consent limit |  |  |  |  | Site being assessed: |  | Pen y Glol Caravan Park
| Drainage layer attenuation factor | AFu1 | 1
| Unsaturated zone attenuation factor | AFu2 | 1 |  |  | Completed by: |  | Nick Rukin (Rukhydro Ltd)
| Concentration at base of drainage layer | Cdl | 243.5714 | mg/l |  | Date: |  | 2024-07-08
| Concentration at base of unsaturated zone | Cwt | 243.5714 | mg/l
|  |  | and |  |  | Version: |  | 1.NO3 likely
| Environmental Permit limit value | EPL1 | 50 | mg/l
Concentration at base of unsaturated zone exceeds target concentration
Note on B17: Vertical dispersivity assumed as 10% of unsaturated zone thickness
Note on B23: Ensure appropriate Kd value is selected, taking account of soil pH and soil organic matter content.
Note on B25: Calculates Kd as: Kd = Koc . foc
Note on B42: Vertical dispersivity assumed as 10% of unsaturated zone thickness
Note on B46: Assumes no retardation or degradation of by-pass component
Note on B49: Ensure appropriate Kd value is selected, taking account of soil pH and soil organic matter content.
Note on B51: Calculates Kd as: Kd = Koc . foc

## Dilution
Infiltration Worksheet
Dilution
| Substance |  | Nitrate |  | From introduction sheet | This sheet calculates the dilution factor for groundwater dilution below the drainage field. Substance concentration in groundwater and discharge consent limit
| Compliance value or environmental standard | CT | 50 | mg/l | From introduction sheet
| Source concentration | Ce | 243.5714 | mg/l | From infiltration sheet
| Concentration at base of drainage layer | Cwt | 243.5714 | mg/l | From atten_unsatzone sheet
| Input Parameters | Variable | Value | Unit | Source of parameter value
Standard entry
| Infiltration | Inf | 0.088235 | m/d | From infiltration sheet
| Area of drainage field | A | 170 | m2 | From infiltration sheet
Entry for groundwater flow below site
| Length of drainage field in direction of groundwater flow | L | 90.9576 | m | 50m + (50xcos35°) to 50+50m |  |  | 1 | Calculate
| Saturated aquifer thickness | da | 250 | m | Range 200 to 300m (Rukhydro GWRA (RP030i1) Section 2.6.5)
| Hydraulic Conductivity of aquifer in which dilution occurs | K | 0.186 | m/d | Based on assumed minimum transmissivity of 43m2/day. Rukhydro (2021) Section 2.6.5
| Hydraulic gradient of water table | i | 0.0148 | fraction | Rukhydro GWRA (RP030i1) Section 2.6.3
| Width of drainage field perpendicular to groundwater flow | w | 57.3576 | m | Trenches splay 35° each side of south, so the furthest tip is 50m x Sin(35°) from south. |  |  |  |  | Calc cells to be hidden
| Background concentration of substance in groundwater up-gradient of site | Cu | 30.4376 | mg/l | Ffynnon Asaph Spring Mean 6.873mg/l N (Rukhydro GWRA (RP031i1) Table 2.8
Define mixing zone depth by specifying or calculating depth (using pull down list) |  |  | Calculate | [6 empty] | 0 | Specify
| Enter mixing zone thickness | Mz | 5 | m |  | Not valid - Value calculated |  |  |  | 1 | Calculate
| Calculated mixing zone thickness | Mz | 250 | m |  | Not valid - Value specified
w * L ( 5217.11373372 ) does not equal area (A) of drainage field ( 170 ) - check parameters used (this may be OK if drainage field at angle to flow direction)
| Groundwater flow (mixing zone) below drainage field | Gw | 39.4735 | m3/d
Dilution factor and discharge consent limit
| Dilution Factor | DF | 3.6316 |  |  |  | Site being assessed: |  | Pen y Glol Caravan Park
| Headroom Factor | HF | 2.0296 |  |  |  | Completed by: |  | Nick Rukin (Rukhydro Ltd)
| Unsaturated zone attenuation factor | AFu | 1 |  | From infiltration sheet |  | Date: |  | 2024-07-08
| Concentration in groundwater below drainage field | Cgw | 89.1268 | mg/l |  |  | Version: |  | 1.NO3 likely
or
| Environmental Permit limit value | EPL2 | 101.4799 | mg/l
Concentration immediately downgradient of drainage field exceeds target concentration
w * L ( 5217.11373372 ) does not equal area (A) of drainage field ( 170 ) - check parameters used (this may be OK if drainage field at angle to flow direction)
5217.1137
w * L (
) does not equal area (A) of drainage field (
) - check parameters used (this may be OK if drainage field at angle to flow direction)
Note on B16: Dilution Factor, DF, calculated as: DF = (Gw + Inf*A)*CT - Gw*CU) / (Inf*A*CT)
Note on B30: Dilution Factor: based on volumetric dilution only. Dilution Factor, DF, calculated as: DF = 1+ ((Gw) / (Inf*A))
Note on B31: Headroom Factor: used in the calculation of the DL2 discharge limit value. This takes into account how much of the 'headroom' remains between the concentration in the mixing zone and the Target Concentration CT. Headroom Factor, HF, calculated as: HF = (Gw + Inf*A)*CT - Gw*CU) / (Inf*A*CT)

## Attenuation_satzone
| Infiltration Worksheet | [11 empty] | 1
[6 empty] | This sheet calculates attenuation factor for the saturated zone; substance concentration at downgradient compliance point and discharge consent limit | [6 empty] | 0
| Attenuation in saturated zone | [11 empty] | 0
| Input Parameters | Variable | Value | Unit | Source | Enter method of defining partition co-efficient (using pull down list)
[6 empty] | User specified value for partition coefficient | [8 empty] | Calculated concentrations for
| Substance |  | Nitrate |  | From introduction sheet | [9 empty] | distance-concentration graph
| Compliance value or environmental standard | CT | 50 | mg/l | From introduction sheet | Entry if specify partition coefficient (option)
| Source concentration | Ce | 243.5714 | mg/l | From infiltration sheet | Soil water partition coefficient |  | Kd | 0 | l/kg
| Dilution Factor | DF | 3.6316 |  | from dilution sheet | Entry for organic chemicals (option)
| Unsaturated zone attenuation factor | AFu | 1 |  | From atten_unsatzone sheet | Fraction of organic carbon in aquifer |  | foc | 0 | fraction
[6 empty] | Organic carbon partition coefficient |  | Koc | 0 | l/kg |  |  |  |  | From calculation sheet
[6 empty] | Soil water partition coefficient |  | Kd | 0 | l/kg |  |  |  |  | Distance m | Concentration mg/l
|  | Variable | Value | Unit | Source of parameter value | [9 empty] | 0 | 89.1268
[15 empty] | 50 | 67.737
| Concentration in groundwater below drainage field | Cgw | 89.1268 | mg/l | from dilution sheet | [9 empty] | 100 | 58.5296
| Option to select degradation | No degradation occurs |  |  |  | Define dispersivity (click brown cell and use pull down list) | [8 empty] | 150 | 53.8806
| Half life for degradation of substance | t1/2 | 1e+100 | days |  |  | Dispersivities 10%, 1%, 0.1% of pathway length | [7 empty] | 200 | 50.9657
| Calculated decay rate | l | 1e-99 | days-1 | calculated (very low value set if no degradation) | [9 empty] | 250 | 48.9217
| Width of drainage field | w | 57.3576 | m | from dilution sheet |  |  |  | Enter value | Calc value | Xu & Eckstein |  |  |  | 300 | 47.3869
| Mixing zone thickness | Mz | 250 | m | from dilution sheet | Longitudinal dispersivity (m) |  | ax | 1e-12 | 100 | 11.772 |  |  |  | 350 | 46.18
| Bulk density of aquifer materials | r | 2.277 | g/cm3 | Assume mineral density of 2.3g/cm3 and then calculate with porosity. | Transverse dispersivity (m) |  | az | 1e-12 | 10 | 1.1772 |  |  |  | 400 | 45.1988 | Calc cells to be hidden
| Effective porosity of aquifer | n | 0.01 | fraction | Rukhydro GWRA (RP030i1) Section 3.5.4. Fracture porosity. | Vertical dispersivity (m) |  | ay | 1e-12 | 1 | 0.11772 |  |  |  | 450 | 44.3808
| Hydraulic gradient | icorr | 0.020424 | fraction | from dilution sheet (adjusted) | Note values of dispersivity must be > 0 | [8 empty] | 500 | 43.6852 | User specified value for partition coefficient
| Hydraulic conductivity of saturated aquifer | K | 0.186 | m/d | from dilution sheet | [9 empty] | 550 | 43.0843 | Calculate for non-polar organic chemicals
| Distance to compliance point | x | 1000 | m | Distance from discharge site to Hendre Fawr sink hole is 3km. | Xu & Eckstein (1995) report ax = 0.83(log10x)2.414 ; az = ax/10, ay = ax/100 are assumed | [8 empty] | 600 | 42.5583
| Option to select time | Use steady state (recommended) |  |  |  | For calculated value, assumes ax = 0.1 *x, az = 0.01 * x, ay = 0.001 * x | [8 empty] | 650 | 42.093
| Enter time | t | 100 | days | time variant options only |  |  |  |  | User defined values for dispersivity |  |  |  |  | 700 | 41.6774
| Time since pollutant entered groundwater | t | 1e+99 | [11 empty] | 750 | 41.3033
0 | Parameters values determined from options | [13 empty] | 800 | 40.9643 | 1 | No degradation occurs
| Partition coefficient | Kd | 0 | l/kg | see options | [9 empty] | 850 | 40.6551 | 0 | Degradation occurs - sorbed and dissolved phases
| Longitudinal dispersivity | ax | 100 | m | see options | [9 empty] | 900 | 40.3716 | 0 | Degradation occurs dissolved phase only
| Transverse dispersivity | az | 10 | m | see options | [9 empty] | 950 | 40.1105 | 1e-99
| Vertical dispersivity | ay | 1 | m | see options | [9 empty] | 1000 | 39.869
[17 empty] | 1 | Use steady state (recommended)
| Calculated Parameters | Variable | Value | Unit | [12 empty] | 0 | Enter time (if validating model)
| Groundwater flow velocity | v | 0.37989 | m/d
| Retardation factor | Rf | 1 | fraction | [7 empty] | Site being assessed: |  | Pen y Glol Caravan Park
| Decay rate used | l | 1e-99 | d-1 | [7 empty] | Completed by: |  | 0 |  |  | Dispersivity based on Xu & Eckstein (1995)
| Hydraulic gradient used in aquifer flow down-gradient | icorr | 0.020424 | fraction | [7 empty] | Date: |  | 0 |  |  | Dispersivities 10%, 1%, 0.1% of pathway length
| Rate of contaminant flow due to retardation | u | 0.37989 | m/d | [7 empty] | Version: |  | 0 |  |  | User defined values for dispersivity
| Attenuation factor | AFs | 6.2227 | fraction
| Attenuation and Dilution factors and discharge consent limit | [7 empty] | Domenico - Time Variant
| Dilution Factor | DF | 3.6316
| Unsaturated zone attenuation factor | AFu | 1
| Saturated zone attenuation factor | AFs | 6.2227
| Concentration in groundwater at compliance point | Cdcp | 39.869 | mg/l | below compliance value
or
| Environmental Permit limit value | EPL3 | 631.4836 | mg/l | Discharge limit for discussion with Environment Agency
| Distance to compliance point |  | 1000 | m
Concentration at compliance point below target concentration
Note on H10: Ensure appropriate Kd value is selected, taking account of aquifer pH and aquifer organic matter content. Calculates Kd as: Kd = Koc . Foc
Note on B18: Half-life of contaminant in days (assumed to be a first order decay rate). If contaminant does not degrade, enter a very large number e.g. 9E+99
Note on B19: First order decay rate: l = 0.693 / t1/2
Note on B24: Hydraulic gradient reclaculated from Dilution sheet to include infiltration over site
Note on B25: Hydraulic conductivity carried forward from Dilution Sheet
Note on B41: A corrected hydraulic gradient is used to ensure mass balance as follows: icorr = I * (DF / DF-1)

## Summary
Infiltration Worksheet
Summary of calculations for concentration of substance in groundwater
No input required,values taken from previous worksheets
Summary of compliance data, attenuation and dilution factors
| Substance |  | Nitrate
| Effluent concentration | Ce | 243.5714 | mg/l
| Compliance value or environmental standard | CT | 50 | mg/l
| Distance to compliance point |  | 1000 | m
| Attenuation factor - unsat zone | AFu | 1
| Dilution Factor | DF | 3.6316
| Attenuation factor- sat zone | AFs | 6.2227
Predicted concentrations at compliance point based on proposed effluent concentration | [5 empty] | Calc cells to be hidden
| Concentration at base of unsaturated zone | Cwt | 243.5714 | mg/l | Attenuation in unsaturated zone only
[6 empty] | Effluent | 243.5714 | 50
| Concentration in groundwater below drainage field | Cgw | 89.1268 | mg/l | Dilution taken into account | Base unsat zone | 243.5714 | 50
[6 empty] | Dilution | 89.1268 | 50
| Concentration in groundwater at compliance point | Cdcp | 39.869 | mg/l | Attenuation in saturated zone taken into account | Compliance borehole | 39.869 | 50
Provisional Environmental Permit limit values
| Based on attenuation in unsaturated zone | EPL1 | 50 | mg/l
| Based on attenuation in unsaturated zone and dilution | EPL2 | 101.4799 | mg/l
| Based on dilution and attenuation in unsaturated and saturated zone | EPL3 | 631.4836 | mg/l | Discharge limit for discussion with Environment Agency

## Simple calcs
Simple hydrogeological calculations
(These calculations are provided to allow additional hydrogeological calculations to be undertaken if required)
| Parameter | symbol |  | unit | justification
| Hydraulic conductivity | K | 0 | m/d
| Hydraulic gradient | i | 0 | unitless
| Effective porosity of aquifer | n | 0 | fraction
| Thickness of saturated aquifer | b | 0 | m
| Width of aquifer perpendicular to flow | w | 0 | m
| Distance to receptor | x | 0 | m
| Bulk density of aquifer materials | r | 0 | g/cm3
| Soil-water partition co-efficient | Kd | 0 | l/kg
| Retardation factor of pollutant | R | #DIV/0!
| Groundwater flow velocity | v(GW) | #DIV/0! | m/s | #DIV/0! | m/day | #DIV/0! | m/year
| Time for groundwater to reach receptor | t(GW) | #DIV/0! | seconds | #DIV/0! | days | #DIV/0! | years
| Rate of groundwater flow through aquifer | Q | 0 | m3/s | 0 | m3/day | 0 | m3/year
| Contaminant flow velocity | v(contam) | #DIV/0! | m/s | #DIV/0! | m/day | #DIV/0! | m/year
| Time for contaminant to reach receptor | t(contam) | #DIV/0! | seconds | #DIV/0! | days | #DIV/0! | years
Note on B7: Aquifer hydraulic conductivity is best obtained from field pumping test analyses. Hydraulic conductivities obtained from cores should be treated with caution as the results will not reflect the impacts of larger scale features such as fissures and fractures present in the aquifer.
Note on B9: Porosity is expressed as a fraction between 0 and 1 (generally between 0.02 and 0.4, depending on rock type). In fissured aquifers and dual porosity aquifers use fissure porosity available for flow, sometimes called kinematic porosity.
Note on B13: Distance to an identified receptor, compliance point, or other location of interest within the aquifer down-hydraulic gradient of the source.
Note on B16: Retardation factor, R, describes the flow velocity of a contaminant relative to groundwater. A conservative contaminant that flows at the same velocity as groundwater has R=1. Other contaminants which are retarded as a result of sorption processes to aquifer minerals and organic matter have R>1. R is calculated from the expression: R = 1 + (Kd . r)/n
Note on B20: Groundwater flow based on darcian hydraulics: v = K.i/n
Note on B21: Calculates travel time assuming darcian flow: t(GW) = x.n / K.i
Note on B22: Calculates flow based on Darcy's Law: Q = K.A.i, where A = b.x
Note on B24: Contaminant flow velocity calculated assuming darcian hydraulics by: v(contam) = K.i / n.R
Note on B25: Time for contaminant to flow to receptor assuming darcian hydraulics: t(contam) = x.n.R / K.i Note: This simple calculation ignores the effects of (longitudinal) dispersion and will therefore OVER-ESTIMATE the time to break-through. (i.e. break-through will actually occur more quickly than calculated with this solution).

## Ammonium calculator
Ammonium calculator
This sheet allows the user to convert between different laboratory analysis for ammonium
The ammonium ion (NH4) is typically the dominant ion at neutral pH , however in more alkaline water the ammonia (NH3) ion becomes increasingly dominant.
Laboratories may report the analysis for ammonium as (NH4) or as N (NH4-N). In some cases the laboratory may have reported the result as Total ammonia (as NH3) or as Total ammonoa as N. In this case total ammonia is likely to include ammonium (NH4) and ammonia (NH3).
In this case NH4 may be been converted to NH3.
Form of ammoniun (laboratory) | Ammonium (NH4) as N |  |  |  |  | Ammonium (NH4) as N | Ammonium as NH4 | Total Ammonia as NH3 | Total Ammonia as N
|  |  | Ammonium (NH4) as N | as N | 4 | 1 | 1.2857 | 1.2143 | 1
Concentration (laboratory) | 10 | mg/l as N | Ammonium as NH4 | as NH4 | 5 | 0.77778 | 1 | 0.94444 | 0.77778
|  |  | Total Ammonia as NH3 | as NH3 | 6 | 0.82353 | 1.0588 | 1 | 0.82353
Unit to convert to | Ammonium as NH4 |  | Total Ammonia as N | as N | 7 | 1 | 1.2857 | 1.2143 | 1
Converted concentration | 12.8571 | mg/l as NH4
as N
as NH4
5
1.2857

## Porosity Calculator
Porosity Calculator
These results are not carried through to any of the other worksheets
DRY BULK DENSITY DATA
Variable | Value | Unit | justification
Natural Moisture Content | 0 | % wt
Particle Density | 0 | tonnes/m3 | (Change this number only if you have specific information)
Dry Bulk Density | 0 | tonnes/m3
Calculated Parameters
Voids Ratio | #DIV/0! | fraction
Initial Saturation | #DIV/0! | %
Total porosity | #DIV/0! | fraction
Air Filled Porosity | #DIV/0! | fraction
Water Filled Porosity | #DIV/0! | fraction
WET BULK DENSITY DATA
Variable | Value | Unit
Moisture Content | 0 | % wt
Particle Density | 0 | tonnes/m3 | (Change this number only if you have specific information)
Actual (wet) Bulk Density ( i.e. at natural MC) | 0 | tonnes/m3
Calculated Parameters
Voids Ratio | #DIV/0! | fraction
dry bulk density | 0 | tonnes/m3
Initial Saturation | #DIV/0! | %
Total porosity | #DIV/0! | fraction | #DIV/0!
Air Filled Porosity | #DIV/0! | fraction
Water Filled Porosity | #DIV/0! | fraction
Analytical solutions provided by David Hall, Golder Associates (UK) Ltd
Note on B8: This number should only be changed if you have specific information
Note on B25: This number should be changed only if you have specific information

## Attenuation calc_sat_zone
Calculation sheet for attenuation in saturated zone
OGATA BANKS SOLUTION
Calculations for source located at top of aquifer (ie vertical dispersion in one direction)
|  |  |  | X | Term 1 | Term 2 | EXP | Term 3 | ERFC | Term 4 | EXP | Term 5 | ERFC | Term 6a | ERF | Term 6b | ERF | Term 7a | ERF | Term 7b | ERF | Relative Concentration | Concentration
Input | Value | Units
CT | 50 | mg/l | 1 | 50 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 0.5 | 1.6487 | 9.7453e+47 | 0 | 0.64128 | 0.63554 | -0.64128 | -0.63554 | 17.6777 | 1 | -17.6777 | -1 | 0.63554 | 67.737
DF | 3.6316 |  | 2 | 100 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 1 | 2.7183 | 9.7453e+47 | 0 | 0.45345 | 0.47866 | -0.45345 | -0.47866 | 12.5 | 1 | -12.5 | -1 | 0.47866 | 58.5296
Cgw | 89.1268 |  | 3 | 150 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 1.5 | 4.4817 | 9.7453e+47 | 0 | 0.37024 | 0.39944 | -0.37024 | -0.39944 | 10.2062 | 1 | -10.2062 | -1 | 0.39944 | 53.8806
|  |  | 4 | 200 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 2 | 7.3891 | 9.7453e+47 | 0 | 0.32064 | 0.34978 | -0.32064 | -0.34978 | 8.8388 | 1 | -8.8388 | -1 | 0.34978 | 50.9657
l | 1e-99 | days-1 | 5 | 250 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 2.5 | 12.1825 | 9.7453e+47 | 0 | 0.28679 | 0.31495 | -0.28679 | -0.31495 | 7.9057 | 1 | -7.9057 | -1 | 0.31495 | 48.9217
Sz | 57.3576 | m | 6 | 300 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 3 | 20.0855 | 9.7453e+47 | 0 | 0.2618 | 0.2888 | -0.2618 | -0.2888 | 7.2169 | 1 | -7.2169 | -1 | 0.2888 | 47.3869
Sy | 250 | m | 7 | 350 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 3.5 | 33.1155 | 9.7453e+47 | 0 | 0.24238 | 0.26823 | -0.24238 | -0.26823 | 6.6815 | 1 | -6.6815 | -1 | 0.26823 | 46.18
Kd | 0 | l/kg | 8 | 400 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 4 | 54.5982 | 9.7453e+47 | 0 | 0.22673 | 0.25152 | -0.22673 | -0.25152 | 6.25 | 1 | -6.25 | -1 | 0.25152 | 45.1988
r | 2.277 | g/cm3 | 9 | 450 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 4.5 | 90.0171 | 9.7453e+47 | 0 | 0.21376 | 0.23758 | -0.21376 | -0.23758 | 5.8926 | 1 | -5.8926 | -1 | 0.23758 | 44.3808
n | 0.01 |  | 10 | 500 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 5 | 148.4132 | 9.7453e+47 | 0 | 0.20279 | 0.22573 | -0.20279 | -0.22573 | 5.5902 | 1 | -5.5902 | -1 | 0.22573 | 43.6852
i | 0.020424 |  | 11 | 550 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 5.5 | 244.6919 | 9.7453e+47 | 0 | 0.19335 | 0.21549 | -0.19335 | -0.21549 | 5.33 | 1 | -5.33 | -1 | 0.21549 | 43.0843
K | 0.186 | m/d | 12 | 600 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 6 | 403.4288 | 9.7453e+47 | 0 | 0.18512 | 0.20652 | -0.18512 | -0.20652 | 5.1031 | 1 | -5.1031 | -1 | 0.20652 | 42.5583
x | 1000 | m | 13 | 650 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 6.5 | 665.1416 | 9.7453e+47 | 0 | 0.17786 | 0.1986 | -0.17786 | -0.1986 | 4.9029 | 1 | -4.9029 | -1 | 0.1986 | 42.093
z | 0 | m | 14 | 700 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 7 | 1096.6332 | 9.7453e+47 | 0 | 0.17139 | 0.19151 | -0.17139 | -0.19151 | 4.7246 | 1 | -4.7246 | -1 | 0.19151 | 41.6774
y | 0 | m | 15 | 750 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 7.5 | 1808.0424 | 9.7453e+47 | 0 | 0.16558 | 0.18514 | -0.16558 | -0.18514 | 4.5644 | 1 | -4.5644 | -1 | 0.18514 | 41.3033
t | 1e+99 | days | 16 | 800 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 8 | 2980.958 | 9.7453e+47 | 0 | 0.16032 | 0.17936 | -0.16032 | -0.17936 | 4.4194 | 1 | -4.4194 | -1 | 0.17936 | 40.9643
ax | 100 | m | 17 | 850 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 8.5 | 4914.7688 | 9.7453e+47 | 0 | 0.15553 | 0.17409 | -0.15553 | -0.17409 | 4.2875 | 1 | -4.2875 | -1 | 0.17409 | 40.6551
az | 10 | m | 18 | 900 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 9 | 8103.0839 | 9.7453e+47 | 0 | 0.15115 | 0.16927 | -0.15115 | -0.16927 | 4.1667 | 1 | -4.1667 | -1 | 0.16927 | 40.3716
ay | 1 | m | 19 | 950 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 9.5 | 13359.7268 | 9.7453e+47 | 0 | 0.14712 | 0.16482 | -0.14712 | -0.16482 | 4.0555 | 1 | -4.0555 | -1 | 0.16482 | 40.1105
Bgd | 30.4376 |  | 20 | 1000 | 0.125 | 0 | 1 | -9.7453e+47 | 2 | 10 | 22026.4658 | 9.7453e+47 | 0 | 0.14339 | 0.1607 | -0.14339 | -0.1607 | 3.9528 | 1 | -3.9528 | -1 | 0.1607 | 39.869
Calc | Value
v | 0.37989 | m/d
Rc | 1
u | 0.37989 | m/d
Date: | 2024-07-08
Version: | 1.NO3 likely