## User Guidance
Duly Making Checklist - New Bespoke and Variations
User Guidance
The following checklist is a tool to aid duly making by duly making officers and should be used alongside the relevant guidance. This checklist should be used for new bespoke and variation applications. If your application is for an Intensive Farm, standalone Medium Combustion Plant (MCP) and/or Specified Generator (SG) or Radioactive Substances (RSR), please use the sector specific checklists. There are also separate checklists for Standard Rules Permits (SRPS), admin variations and surrenders. The duly making officer should mark sections of the checklist that don't apply as 'N/A'. Guidance notes (pink text) have been included to help officers determine requirements, these can be deleted and replaced by your own notes relating the application. Where information has been identified as missing during the checks, use your judgement to decide if the application should be returned or if the information can be requested from the Applicant. As a general rule, if you do not believe the information can be provided within 10 working days, the application should be returned and the Applicant will need to re-apply. There may be circumstances where need to consider asking for extra plans and/or information or we may decide something isn’t required. Officers should use their professional judgement based on regulatory experience in these cases. If you are planning on asking for information or plans not covered by this checklist this should be agreed with an LSO or sector lead and the reasons why they are needed should be shared with the Applicant.
Generic Guidance
OGN 252: Duly Making Permit Applications
Regulatory Guidance Note 3: Deciding applications are duly made and requests for further information
Application Form Guidance Notes Part A
Application Form Guidance Notes Part B2 - General
Application Form Guidance Notes Part B3 - Apply for Bespoke Installation Activities
Application Form Guidance Note Part F1 - Opra, Charges and Declarations

## Application Details
Dates |  | Process Checklist |  | Completed? | Guidance / Notes
Permitting Officer name |  | 1 | Update PALS, allocating the application to yourself
Date application received | 2025-02-14 | 2 | Notify the Applicant that the application has been allocated to a PO
Date application allocated |  | 3 | Notify the relevant Regulation Team and/or Site Officer (for variations/surrenders) that the application has been allocated to a PO
Duly made decision date | Date you decide if application is duly made or not duly made | 4 | Familiarise yourself with the application to understand the proposal
Not duly made date | Only relevant if applicant is not duly made | 5 | Check if there has been any pre-application correspondence and discuss with Site Officer if required
Duly made date | If application is duly made straight away then this will be the date the application was received. If further information was requested, this will be the date the additional information was received. | 6 | Complete duly making checklist |  | If payment has not been received, no further checks on the application should be carried out. Request payment from the applicant and inform them that no further checks will be carried out unless payment is received within one week. If payment had not been received by the deadline, application will be not duly made and potentially returned.
|  | 7 | If the application can be Duly Made, draft Duly Made Letter
Application Information |  | 8 | If further information is required, draft a Not Duly Made Letter - Request for Further Information Letter
Site / Facility Name | Hyppo Hydrogen Solutions Bay Studios | 9 | If you decide the application needs to be returned straight away, draft Return Letter |  | Application should only be returned straight away if missing information cannot be reasonably provided within 10 working days.
Applicant Name | Hyppo Hydrogen Solutions Ltd | 10 | Arrange for a Duly Making peer review (if required) |  | This is not a requirement for every application but you can get your duly made decision and letter checked by another Officer (e.g. if you are a new starter, the application is for a sector you are less experienced in and/or if the application is for something new or novel)
Application reference (PAN) | PAN-028357 | 11 | Send Letter to Applicant
Variation number | N/A | 12 | Update PALS / DMS |  | Remember to also save your completed duly making checklist to DMS as 'to be assessed' as a record of our decision making.
DMS Link | PAN-028357 | 13 | Review additional information submitted |  | N/A where applications are duly made upon receipt
Summary of proposal | Production of Hydrogen by electrolysis using a polymer electrolyte membrane and using electricity from renewable sources. Electrolyser is 175 kw. | 14 | If additional information received is not adequate or the information is not received by the deadline specified, return the application. If additional information is sufficient, duly make the application following steps 7, 11 and 12. |  | N/A where applications are duly made upon receipt. Note that the duly made in this scenario is the date the additional information is received.
Have there been any pre-application discussions? | No | 15 | All varaition with a Landfill -Landfill disposals tax team notification Notify Jacob Birch (Team leader) at Jacob.Birch@cyfoethnaturiolcymru.gov.uk or the Landfill Disposals Tax team at LDT@cyfoethnaturiolcymru.gov.uk. Any landfill related application. Include link to the DMS folder |  | N/A for non Landfill permits
Is the application considered to be of high public interest (HPI)? | No
Is the application for a 'Nationally Significant Infrastructure' project? | No
Has the application bee subject to a previous refusal? | No
Is the application for a new or novel activity? | No

## Triage
**Spend no more that one hour on triage**
Application Fee | Yes / No / N/A | Comments / Guidance Notes | Links
Have we received a fee? | Yes | £788 for quick hydrogen permit received on 14/02/25 | Natural Resources Wales / Our Charges
Is the application fee correct? | Yes
Application type | Yes / No / N/A | Comments / Guidance Notes | Links
Has the Applicant applied for the correct application type? If it is an Admin variation, check it is complete and pass it on to the PSOs for processing. | Yes |  | Natural Resources Wales / Our Charges | Substantial changes in operation at installations, mining waste facilities and other facilities involving solvent and combustion (cyfoethnaturiol.cymru)
Has the Applicant applied for the correct activity type? | Yes |  | Environmental Permitting (England and Wales) Regulations 2016 | Understanding the meaning of Regulated Facility
Has the Applicant completed the correct application forms? | Yes |  | Apply for an Environmental Permit for a new installation
Have the application forms declaration been signed by an appropriate person? | Yes | Company Director Signature | Application Form Part F1 Guidance
Key aspects of the application | Yes / No / N/A | Comments / Guidance | Links
Considering the application type, complete a quick check to ensure the main documents associated with that application type are present. | Yes
If Air, Noise and / or Odour modelling has been completed, check that the relevant modelling files have been included with the application. | N/A
Next steps | Yes / No / N/A | Comments / Guidance Notes | Links
Complete the parts highlighted yellow in the Application Details tab | Yes
Set up a Time Recording spreadsheet for the application and save it in the Time Recording DMS folder | Yes |  | https://cyfoethnaturiolcymru.sharepoint.com/teams/manbus/ManagingRegionsAndGroups/hbreksp/RBMT/Forms/NRW%20View.aspx?RootFolder=%2Fteams%2Fmanbus%2FManagingRegionsAndGroups%2Fhbreksp%2FRBMT%2FTime%20Recording%2FInstallations&FolderCTID=0x012000F3F7A7463E79EE479C3AA7ECFB439110&View=%7BD26555FB-E3DB-45BF-ADA6-DAC08EC4DD99%7D
Add that Triage has been completed and any important information to the 'Triage Status' column of the relevent row for the application in the 'Unallocated' tab on the TIB | Yes
Send an email from the Installations inbox to the applicant outlining what pieces of information are missing from the application using the Standard Email text, copying in Holly. | Yes | Email sent 12/03/25 requesting - statement of site condition, emission point confirmation and labelling on Site Plan, confirmation of if process waste water is discharged to sewer or tankered off site. Requested Trade Effluent Consent from Welsh Water if the former applies.
Set up a WIP folder for the application | Yes
Save the Duly Making checklist to the DMS folder as 'not public register'. | Yes
Standard Email text
Dear X,
We have received your application ref PAN-xxxxx.
Whilst your application sits on our work queue we have completed a high-level check of it for completeness. The check was not exhaustive, but our initial observations indicate that you may wish to consider supplying or revising the following:
X
X
X
Once allocated to a permitting officer for determination, your application will undergo a more thorough assessment and there are likely to be further requests for information or queries at this stage. It will help us complete this assessment more quickly if you consider the points listed above now and if appropriate, supply us with any additional information before the assessment starts.
Any supplements to your application should be submitted via the Permit Receipt Team permitreceiptcentre@cyfoethnaturiolcymru.gov.uk, quoting your PAN reference number so that it can be added to your application.
Kind regards
Installations Permittting

## General
Application Fee | Yes / No / N/A | Comments / Guidance Notes | Links
Has the applicant submitted a charge tool spreadsheet (Tier 3 bespoke) |  | Check that the applicant has used the correct charge tool (All New bespokes use the bespoke charge tool and Variations use the variation charge tool) | OPRA - NRW View (sharepoint.com)
Is the charge tool correct and up to date |  | Check the tool uses the current financial year charges (when the application was submitted) in line with the charge guidance
Is the application fee paid correct and in line with the current charging scheme? |  | Check Teir 2 fixed charges and Teir 3 (charge tool) are up to date
Has the OPRA profile spreadsheet been provided and is it correct |  | Check against current charging scheme. | Natural Resources Wales / Our Charges
Has the fee been received? |  | The fee should have been checked when the application was received, please see TIB Board. If not, check MyNRW (Reports > Permitting Enquiries > Permitting Receipts Enquiry). If the payment isn't showing on MyNRW, ask the applicant for proof of payment or to make payment. If the applicant is not able to provide proof of payment / payment has still not been made, no further duly makes should be made and the application should be returned. | MyNRW
Has an advertising fee been paid? |  | Only relevant for High Public Interest (HPI) applications (discuss with Team Leader)
General requirements | Yes / No / N/A | Comments / Guidance Notes | Links
Have the correct application forms been used? |  |  | Natural Resources Wales / Apply for a bespoke permit for an installation
Has the Applicant applied for the correct application type? |  | See charging scheme and charging scheme guidance for guidance on variation types. | Natural Resources Wales / Our Charges | Substantial changes in operation at installations, mining waste facilities and other facilities involving solvent and combustion (cyfoethnaturiol.cymru)
Have the application forms declaration been signed by an appropriate person? |  | See application form Part F1, section 7d. For guidance on who is a 'appropriate person' see application form Part F1 guidance. | Application Form Part F1 Guidance
Are all relevant parts of the application forms completed?
Are the supporting documents suitably referenced? |  | See application form Part F1, section 6. Use your judgement to decide if the supporting information referred to in the application forms is easily identifiable.
Has the Applicant applied for the correct Part A activity? |  |  | The Environmental Permitting (England and Wales) Regulations 2016 (legislation.gov.uk)
Have all the relevant Directly Associated Activities (DAA) been identified? |  | Activities which are carried our on the site , have a technical connection with the with the main activity being carried and could have an effect on pollution. | Regulatory Guidance Note No. 2 Understanding the meaning of regulated facility - Appendices 1 and 2 (publishing.service.gov.uk)
Have activities within a Statutory Technical Unit (STU) been identified where relevant? |  | Activities which are a Part A activity but also a Part A(2) and Part B activity.
Has a sufficient non-technical summary of the application been provided? |  | See Application Form Part B2, section 5c. For variations, this should clearly explain what parts of the permit the Applicant wants changing and why.
Have process flow diagrams and/or technical drawings been included? |  | Only required in certain scenarios. Use your judgement on whether these are needed depending on the proposal.
Has a sufficient site plan been submitted? |  | See Application Form B2 (or C2 for variations), section 5. The site plan should clearly show the installation boundary (in green) and emission points. Check the boundary includes all relevant parts of the 'installation' See application form guidance for further guidance on what is expected of a site plan. | Application Form Part B2 Guidance
Commercial Confidentiality and National Security | Yes / No / N/A | Comments / Guidance | Links
Has the applicant applied for commercially confidentiality in respect of the application? |  | See application form Part F1, section 5. | Environmental permitting: Core guidance (publishing.service.gov.uk) | On-line Public Register Guide - Using DMS metadata correctly_Final v4 Nov19.docx (sharepoint.com) | https://cdn.cyfoethnaturiol.cymru/media/687071/part-f1_guidance-v2_final.pdf
If commercial confidentiality has been applied for, has the Applicant clearly identified what parts of the application they wish to be considered as commercially confidential and have they provided clear justification? |  | Any application for commercial confidentiality will be assessed during determination. At duly making, we need to have all the information we need to decide if it can be granted. See EPR Core Guidance, section 14 for more information. If it has been applied for, ensure the relevant information has been marked as 'to be assessed' at duly making stage until a decision has been made.
Has the applicant claimed national security for the application? |  | See application form Part F1, section 5.
If national security has been claimed, has the Applicant included a letter with the application stating they have written to Welsh Ministers to claim national security? |  | National security cannot be applied for via an Installations application. The decision is to be made by Welsh Government and we cannot progress the application until we have received confirmation of the decision from Welsh Government. If no letter has been provided confirming they have applied to Welsh Ministers, the application is not duly made. If a letter has been provided, speak to your Team Leader and/or Lead Specialist Officer on next steps prior to duly making the application.
Operator Competence | Yes / No / N/A | Comments / Guidance Notes | Links
Has the 'Operator' been identified correctly and is the 'legal entity' correct? |  | See application form Part A, sections 1-5. See Regulatory Guidance Note 1: Understanding the meaning of Operator for guidance. | Regulatory Guidance Note 5: Operator Competence
Has a summary of (or updated summary) the Environmental Management System (EMS) been submitted and is it sufficient? |  | See application form Part B2 (or C2 for variations) section 3d. The summary must contain enough information for us to check whether the full system meets the standards in our guidance. Check to see if the sections we would expect have been included and if the content of each section is in line with what if required as outlined in 'How to comply with your Environmental Permit' If the applicant has claimed they have an accredited EMS (e.g. ISO 14001) and has provided a certificate as evidence, no further information is required. | Natural Resources Wales / Guidance to help you comply with your Environmental Permit
Have relevant offences been declared on the application form? |  | See application Form Part B2 section 3a. Check using NRW's COLINS system. | Relevant convictions for waste and installations environmental permits - GOV.UK (www.gov.uk)
RGN1 Understanding the Meaning of Operator
COLINS - Home Page (cyfoethnaturiol.cymru)
Has sufficient evidence of the Applicant's technical competence been provided with the application? |  | See Application Form Part B2 (C2 for variation), section 3b. Only relevant where a installation waste operation is the permits primary activity. For variations, where the required technical competence will change, then the correct award must have been obtained prior to the permitted operation becoming operational (where the technical competence requirement is not changing then NA) For new permits, the correct award must have been obtained prior to the permitted operation becoming operational. For the purpose of duly making, the Applicant where possible should confirm who the technically competent manager will be, what relevant qualification they will have and expected completion date. For sites with long leading times this is often not possible.
If the applicant (or any relevant persons) declared that they have current or past bankruptcy or insolvency proceedings against them, have they provided details of these proceedings? |  | See Application Form Part B2, section 3b Not required for variations. If yes, the Applicant must provide the relevant information. See application form guidance for more information.
Has the Applicant confirmed how financial provision will be made and has an expenditure plan been submitted? |  | Only required for Landfills, Category A mining waste facilities and mining waste facilities for hazardous waste
Site Condition Report (SCR) | Yes / No / N/A | Comments / Guidance Notes | Links
if required, has the applicant provided a SCR? |  | See application form Part B2 (or C2 for variation, section 5b. Only required for new installations or variations where include extending the installation boundary. | Environmental Permitting Regulations , Guidance for applicants H5, Site Condition Report, Guidance and Template (cyfoethnaturiol.cymru) | SCR template (cyfoethnaturiol.cymru) | part-b2_guidance_final.pdf (cyfoethnaturiol.cymru)
Does the SCR include all the sections we would expect? |  | Sections should be included as outlined in Horizontal Guidance 5 H5 - Site conditions Report / Template.
Is the content of each section in line with what is required? |  | As set out in H5 - site Condition Report.
Energy Efficiency | Yes / No / N/A | Comments / Guidance Notes | Links
Does the application described the energy efficiency measures? |  | Consider if a clear energy balance is required. | https://www.gov.uk/guidance/energy-efficiency-standards-for-industrial-plants-to-get-environmental-permits
Has an energy efficiency assessment been provided? |  | Required for energy intensive activities i.e. energy from waste, combustion, food and drink, refineries, textiles, non-ferrous metals.
Does the Application include an assessment of options to utilise waste heat based on the Environment Agency CHP (Combined Heat and Power) ready external guidance note? |  | Only required if the application is for a new power station or a variation to add >50MWth combustion unit. | Energy efficiency for combustion and energy from waste power plants - GOV.UK (www.gov.uk)
Has Article 14 of the Energy Efficiency Directive been considered? |  | Only required for applications for combustion activities proposing a plant with aggregated net thermal input of >20 MWth

## BAT
Best Available Techniques (BAT) | Yes / No / N/A | Comments / Guidance Notes | Links
Has a BAT Assessment been provided justifying that BAT has been applied? |  | This is a key aspect of an application. The assessment should identify which BAT conclusions (BATc) apply to their specific activity and how they are going to follow that BAT conclusion and meet any specified BAT-associated emission levels. Where it is proposed BAT is not going to be followed, an alternative technique should be proposed and justified. | Best available techniques: environmental permits - GOV.UK (www.gov.uk) | BAT Reference Documents
Where relevant has an assessment been completed for any secondary BAT conclusions?
If it is proposed BAT is not going to be followed, has an alternative technique been proposed and has this been justified?
If the BAT Assessment refers to supporting information, has this been provided? |  | e.g. waste acceptance procedures, management plans, monitoring plans etc.

## Risk Assessment
Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
Has a generic Environmental Risk Assessment (ERA) been submitted? |  | Document should be referenced in Application Form Part B2, section 6. The assessment should assess each of the risks the proposed regulated facility (or changes to the regulated facility) poses to the environment. This should use the H1 or equivalent method (source, pathway, receptor) The Applicant may submit various ERA's depending on the application type and/or the proposal. For example there are separate risk assessment tests that can be completed for emissions to air and discharges to land. The requirement for an ERA may also be superseded where detailed modelling/assessment has been provided. Use you judgement, the checks below and/or speak to the sector lead to decide if what has been submitted is sufficient. | Risk assessments for your environmental permit - GOV.UK (www.gov.uk)
Has the ERA identified all relevant risks from the site and sources of those risks?
Does the ERA assess risks from fugitive emissions?
Has the ERA identified all relevant receptors at risk from the activity / changes to the activity? |  | Use MyMap for Permitting to run relevant reports to check for statutory protected sites (SACs, SPAs, RAMSARS, SSSIs) and non-statutory sites (Ancient Woodlands, Local Wildlife Sites, National Nature Reserves). You can also check for other receptors such as non designated watercourses, domestic dwellings, schools, hospitals, public buildings, foot paths etc.
Has the ERA identified possible pathways from the sources to the receptors?
Has the ERA assessed the risk level all identified pathways? |  | i.e. low, medium or high risks
Does the ERA detail control measures where risks are identified as high? |  | Consider whether further modelling and/or assessment is required

## Air
Environmental Risk Assessment - Emissions to Air | Yes / No / N/A | Comments / Guidance Notes | Links
Where a proposal includes new or changes to air emissions from a facility, has a standalone risk assessment for air emissions (screening) been provided in line with current guidance? |  | The Applicant should assess the impact of emission to air using the methodology set our in Environment Agency guidance (see link). If detailed dispersion modelling has been provided, this requirement may superseded. | Air emissions risk assessment for your environmental permit - GOV.UK (www.gov.uk)
Where relevant, has a copy of the Applicants H1 tool been provided and is it sufficient? |  | If detailed dispersion modelling has been provided, this requirement will be superseded. | Risk assessments for specific activities: environmental permits - GOV.UK (www.gov.uk)
Have the emission points and pollutants been correctly identified? |  | Check BAT conclusion document for more guidance and/or speak to sector lead.
Do the concentrations for air emissions use the correct oxygen reference conditions? |  | In relation to emissions from combustion processes, the concentration in dry air at a temperature of 273K, at a pressure of 101.3 kPa and with an oxygen content of : 5% for landfill / AD gas engines, 15% for engines/turbines, but usually using MCP/SG template, 3% for all other processes dry for liquid and gaseous fuels, 6% dry for solid fuels [11%] for incineration, but usually using incineration template; a For emissions from non-combustion sources, the concentration at a temperature of 273K and at a pressure of 101.3 kPa, with no correction for water vapour content.
Have the effective stack heights been stated (accounting for buildings if applicable)?
Have emission rates been stated? Are these based on actual measurements and where not, has justification been provided for estimations?
Have the pollutants been quantified? |  | Worse case concentrations should be assumed. Where applicable check if modelled at BAT ELVs. If a BAT ELV does apply and they have modelled at a higher concentration, the application is not duly made (check if a derogation has been applied for). If a lower concentration is modelled, inform the Applicant that this is likely to form the basis of their site-specific ELV. For variations, the assessment should compare the proposal to the exsisting permit ELV s as a worst case scenario assessment unless alternative values are accompanied with monitoring results (unless variation is to increase ELV).
Does the risk assessment compare predicted concentrations against the correct environmental quality standards (EQS)? |  | See EA guidance on air emission risk assessments for environmental permit. EQS both for human health protection and ecological receptors should be considered (sometimes the limits may be different, e.g. NOX/NO2). If an operator derived environmental assessment level (EAL) has been proposed/used, check to see if justification has been provided.
Does the risk assessment assess impact at relevant protected sites? |  | All Special Protection Areas (SPA), Special Area of Conservation (SAC) and Ramsar sites within 10km All Sites of Special Scientific Interest (SSS), Ancient Woodlands, Local Wildlife Sites and National and Local Nature Reserves within 10km. Use MyMap for permitting to check. | Sign In - cyfoethnaturiolcymru.internal
Have background pollutant levels and has justification for figures used been provided? |  | For stage 2 screening assessment only. Justification should be proportionate to risk/site-specific scenario.
Environmental Risk Assessment - Emissions to air Detailed Modelling | Yes / No / N/A | Comments / Guidance Notes | Links
If emissions did not "screen out" following risk assessment, has the applicant provided detailed modelling? |  |  | Environmental permitting: air dispersion modelling reports - GOV.UK (www.gov.uk)
Does the detailed modelling report ('the report') include a location map showing installation boundary and surrounding features?
Does the report provide a list emissions modelled including chemical specification and relevant environmental standard for each substance?
Does the report include background concentrations of the relevant pollutant? |  | The source of the background data must be included and justified.
Does the report explain and justify the model used? |  | Details must include the dispersion modelling software used, software named, type of model and supplier.
Does the report include emission parameters? These should include: Stack location Stack height (m) Pollutant emission rate (g/s) Exit diameter (m) Exit temperature (K, degrees Celsius) In some instances, we may also require: Efflux velocity (actual, m/s) Volumetric flowrate (actual, m3/s) Moisture and Oxygen content at stack exit condition
Does the report detail pollutant concentration, flow and emission rates (g/s)? |  | Emission limit values should be given. These correspond to gas flowrate at the reference conditions) Multiplying the two gives the mass emission rate.
Does the report justify the model receptor grid used? |  | Usually related to stack height.
Does the report provide details of discrete receptors used to assess impact at sensitive locations? |  | Detail should include grid reference location used to assess impact.
Does the report include meteorology data used? |  | The report should include: - chosen met station (and why is it representative) OR confirmation as to if Numerical Weather Prediction (NWP) has been used. - number of years covered by the data (recommended 5, but minimum of 3) - what met year data has been used (e.g. 2012 - 2017) - source of the data (e.g. Uk Met Office) - description of data and uncertainties relating to any alternative metrological data - format of the data (hourly sequential or long term statistical). - wind-rose for each year used
Does the report detail surface characteristics? |  | Details of the surface characteristics at both the met station and modelled domain need to be included .Refers to land-use classification & parameter values e.g. roughness length. This detail may be included in the modelling files so consider use your judgement to decide if the information needs to be requested for the purpose of duly making (speak to LSO for further guidance).
Does the report include details of the buildings included in the model? |  | The report should justify why buildings have been included in the model (or not). If included, the report should detailed the location and dimensions of all buildings including the grid reference, height width and rotation. A location plan showing building location and relative orientation should be provided. Some of this detail may be included in the modelling files so consider use your judgement to decide if the information needs to be requested for the purpose of duly making (speak to LSO for further guidance).
Does the report include details of the terrain included in the model? |  | The report should explain the source, format and processing of digital terrain data used in the model. If terrain hasn't been included in the model, the report should justify why.
Does the report detail how sensitivity analysis has been carried out? |  | It must be shown how the model is affected by variations in met data, emission parameters, receptor grid resolutions and treatment of terrain and buildings.
Does the report clearly present the predicted process contributions (PC) |  | The annual mean and percentile output should be expressed for each pollutant consistent with Air Quality legislation. The report should detail any pollutant conversion assumptions made.
Does the report detail and justify any special model treatments applied? |  | e.g. coastal models, fluctuations, wet or dry deposition
Does the detailed assessment consider abnormal operation impacts? |  | Only relevant for energy from waste sector.
Have results of the modelling been clearly presented? |  | Predicted Process Contributions (PC) and Predicted Environmental Concentrations (PEC) (PC plus ambient background concentration values) should be presented in a table along with the percentages of the relevant environmental standard for air.
Does the report use the modelling results to assess impact upon local air quality in line with guidance? |  | The report should assess significance of results in line with guidance. The report should include a discussion of results and a final conclusion. Breaches of environmental standards should be commented on.
Have contoured plots been provided? |  | The report must include contour plots for each air quality objective assessed.
Have modelling files been submitted (in electronic format)?

## Water
Environmental Risk Assessment - Emission to Surface Water | Yes / No / N/A | Comments / Guidance Notes | Links
Where a proposal includes new or changes to surface water emissions from a facility, has a standalone risk assessment for emission to surface water been provided in line with current guidance? |  | Note that where a proposal includes discharge of surface water off clean uncontaminated water (e.g. surface water run-off), no risk assessment is required. Note that there are separate risk assessments for discharging 'hazardous chemical and elements' and 'sanitary and other pollutants'. See linked guidance for more information. | Surface water pollution risk assessment for your environmental permit - GOV.UK (www.gov.uk) | H1 Annex D2 Assessment of Sanitary and other pollutants in Surface Water Discharges - GOV.UK (www.gov.uk)
If the H1 software tool has been used, has the output been provided? |  | Only needs to be provided where the Application claims the discharge screens out.
Does the risk assessment(s) clearly identify the emission points (discharge points) and discharge arrangement ?
Does the risk assessment(s) correctly identify the pollutants released from the proposed facility? |  | Check the relevant BRef and speak to Water Quality Team/lead. If no, the application is not duly made.
Does the risk assessment(s) include data on pollutant concentrations? |  | Worse case concentrations should be assumed for pollutant concentration. Where applicable check if modelled at BAT ELVs.
Has the risk assessment(s) used maximum and average discharge rates using actual measurements or where estimated, has sufficient justification been used? |  | Discharge rates should include maximum and average flow using actual measurements (with a sufficient sample size). Where discharge flow has been estimates, justification needs to be provided. If discharge rates have been calculated using Greenfield Run-off Rates, make sure the calculations have been provided.
Does the risk assessment(s) use the correct Environmental Quality Standards (EQS) and/or Environmental Assessment Levels for assessment? |  | Check spreadsheets. If unsure, speak to Water Quality Team/lead. | Freshwaters_specific_pollutants_and_operational_environmental_quality_standards.ods (live.com) | Freshwaters_priority_hazardous_substances__priority_substances_and_other_pollutants_environmental_quality_standards__1_.ods (live.com)
For assessment of hazardous chemicals and elements, where the risk assessment does not screen out a pollutant at stage 1 or 2, has the background data used for test 3 and 4 been provided?
Does the risk assessment(s) identify any National Site Network Sites, Sites of Scientific Interest (SSS) or other relevant designations? |  | Check MyMap for permitting. | MyMap for Permitting
Does the risk assessment/application show that the proposal will be increasing concentrations of Phosphorus? |  | This may not effect your duly making decision but it is something that you may want to talk to you applicant about considering the current policy position. | Natural Resources Wales / Advice to planning authorities for planning applications affecting phosphorus sensitive river Special Areas of Conservation
Where the environmental risk assessment requires further assessment, including modelling, has this been supplied and has it been completed in line with the guidance? |  | If no, check with the Water Quality Team if this is something NRW will want to do in-house during determination. | Modelling: surface water pollution risk assessment - GOV.UK (www.gov.uk)
Environmental Risk Assessment - Emissions to Sewer | Yes / No / N/A | Comments / Guidance Notes | Links
Where a proposal includes new or changes to discharges to sewer, have details of the trade effluent been provided? |  | e.g. any limits set, the sewage treatment works name and location of discharge point
Environmental Risk Assessment - Emissions to ground and/or groundwater | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has a groundwater and/or groundwater risk assessment been submitted and has it been completed in line with guidance? Does the surface run off contain any (Hazardous) containments |  | Note- If waste Site discharge to ground is not accetaple if water run off is from area where waste is contained | Groundwater risk assessment for your environmental permit - GOV.UK (www.gov.uk)

## Noise
Noise Impact Assessment (NIA) | Yes / No / N/A | Comments / Guidance Notes | Links
Has a NIA been submitted if required?. Note for variations to installations that can not shut down and take a proper background: if the proposal is <10 db below background we can proceed as low risk |  | In accordance with Sch 7 (4) of EPR2016 and article 12 of IED all Applicants must undertake a noise risk assessment and propose technology and other techniques for preventing or, where this is not possible, reducing emissions from the installation. For lower risk proposals this may be quantitative only. For medium to high risk proposals a noise impact assessment (NIA) based on BS4142:2014+A1:2019 – ‘Methods for rating and assessing industrial and commercial sound’ and a Noise Management Plan based on the results of the NIA must be provided. For new applications, you can use the EA Qualative Noise Screening Tool to help determine if a full NIA is required (see links). For variations, consider if the new/change of activity has the potensial for significnat additional noise pollution. The impact of the whole site following the variation should be presented, not just the impact from the additional noise source. See EA guidance on risk assessments for further guidance on when a Noise Impact Assessment is required. | Noise and vibration management: environmental permits - GOV.UK (www.gov.uk) | EA Qualative Noise Screening Tool
Has the assessment been done in line with BS 4142:2014 standard? Use the further checks below to assess this further. |  |  | BS4142_2014.pdf (sharepoint.com)
Does the NIA include a measurement and description of sources being assessed, including: - the main sound sources and specific sound - operational times, including operational times of plant - description of site layout and location of main sound sources? |  | Sources that form the basis of the EPR application should be clearly stated, and, if applicable, any concurrent non-NRW regulated onsite activities.
Does the NIA include a statement of competency for all persons contributing to the assessment?
Does the NIA include identify the nearest sensitive receptors and description of the existing context, including an assessment of the sensitivity of the receptor, e.g. school, dwelling, office?
Does the NIA include a plan showing measurement locations and description including distance from sound source, intervening ground. A justification for the choice of measurement locations should also be included?
Does the NIA include detail on equipment used, including calibrator or pistonphone: - type and/or model; - manufacturer; - serial number; and - details of the latest verification test including dates?
Does the NIA include details of field calibration tests, including meter reading(s) before and after measurements with calibrator?
Does the NIA include detail on weather conditions, including wind speed(s) and direction(s), precipitation, temperature, etc?
Does the NIA include date(s) and time(s) of measurements?
Does the NIA include details on sound levels and method of determination for residual, ambient and specific ratings? |  | If ambient and residual sound could not be measured (e.g. non-operational site), the specific levels may have been modelled / calculated. Where residual and ambient have been measured the difference must be greater than 3dB. If not a combination of measurements and calculation / modelling may be used. Justification for the method used should be included.
Does the NIA include details on the background sound level(s) (LA90) and measurement time interval(s) and, in the case of measurements taken at an equivalent location, the reasons for presuming it to be equivalent? |  | The site should not be operational during a background sound measurement. If a surrogate locataion has been used, justification should be provided and must be representative of the site locataion.
Does the NIA include details on rating level(s) (specific sound level plus any acoustic features of the specific sound)?
Does the NIA include a initial impact assessment (excess of the rating level(s) over the measured background sound level)?
Does the NIA include conclusions of the assessment after taking context into account?
Does the NIA include the potential impact of uncertainty?
Where the NIA concludes significant adverse impact (taking account of context), have mitigation / controls been included to prevent or minimise impact? Have these been quantified in decibels? |  | Full details/dimensions should be provided as well as the acoustic properties of any enclosure or barrier proposed.
Does the NIA consider all the noise resulting from the proposed variation – the existing site and the variation together? Both components should be shown and then added together to give a new total for site noise at the receptors.
Have modelling files been submitted (in electronic format)? |  |  | Noise impact assessments involving calculations or modelling - GOV.UK (www.gov.uk)
Noise Management Plant (NMP) | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | For medium to high risk proposals a Noise Management Plan based on the results of the NIA must be provided. See EA guidance on risk assessments for further guidance on when a Noise Management Plan is required. | Risk assessments for your environmental permit - GOV.UK (www.gov.uk)
Does the NMP include a commitment to regularly review the effectiveness of the NMP? |  |  | Noise and vibration management: environmental permits - GOV.UK (www.gov.uk)
Does the NMP include a commitment to ensure noise control equipment is designed, operated and maintained appropriately?
Does the NMP include identify sources of noise in normal and abnormal situations?
Does the NMP include a identify any anticipated incidents that may influence noise risk, e.g., weather, breakdowns etc.?
Does the NMP include a detail appropriate controls (measures) to manage identified risks?
Does the NMP include details of monitoring?
Does the NMP include a include details of actions, contingencies and responsibilities if problems arise?
Does the NMP include a inlcude procedures in place to avoid serious noise pollution e.g. reducing / ceasing operations?
Does the NMP include information neighbours will be engaged with?
Does the NMP include a include a compliants procedure?

## Odour
Odour Impact Assessment (OIA) | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has odour modelling been completed and has a Odour Impact Assessment (OIA) using the results been provided with the application? |  | Modelling should be provided where a risk assessment has indicated there is a odour risk to nearby receptors. | Horizontal Guidance Note 4: Odour Management
Does the OIA include the type of dispersion modelling used? |  | This is usually the same as would have been used for the air quality assessment.
Has the OIA modelled impacts over at least 3, preferably 5, metrological years using suitable metrological data? |  | Metrological data should be rom a representative meteorological station or on site weather station. If these data sets are not available, justification for the data used needs to be provided.
Have all potential odour sources been identified ?
Does the OIA detail how odour emission factors have been derived and do these appear reasonable? |  | Where required (HPI or sites of concern) If odour emission rates have been derived from monitoring at a site, the monitoring report, lab anaysis certifcate/report and the calculation method should be provided. If odour emission rates have been obtained from literature, full details should be provided.
Have all receptors been correctly identified? |  | Check MyMap / Google Maps. | MyMap for Permitting
Does the Odour Modelling Report assess the results of the odour modelling in line with Appendix 3 of Horizontal Guidance Note 4: Odour Management? |  | Must include what benchmark they are assessing their predictions against (as outlined in H4 guidance).
Have modelling files been submitted (in electronic format)?
Odour Management Plans (OMP) | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  |  | Environmental permitting: H4 odour management - GOV.UK (www.gov.uk) | EA How to comply with your Intensive Farming Appendices 1-6 (see Appendix 4: Odour management at intensive livestock installations) | https://cyfoethnaturiolcymru.sharepoint.com/teams/Regulatory/ind/odour/PolicyAdviceGuidance/Forms/NRW%20View.aspx?RootFolder=%2Fteams%2FRegulatory%2Find%2Fodour%2FPolicyAdviceGuidance%2FOMP&FolderCTID=0x01200092F825C91615A34EB10C0BAE1EB5F640&View=%7BD7435C1B%2D5409%2D4E03%2D961C%2DBFAA544A8359%7D | Control and monitor emissions for your environmental permit - GOV.UK (www.gov.uk)
Does the OMP clearly relate to the activities proposed and is it structured?
Does the OMP include a complete inventory of odorous material help on site (feedstocks, raw materials, intermediates and wastes)? |  | The inventory might include: - quality limits (waste reception, in treatment and product if applicable - waste types and quantity, including description and EWC (if relevant) - age of waste - storage / treatment method and location - storage time limits - associated monitoring and records for all the above
Does the OMP identify the correct emission points, receptors impacts ? |  | This can refer to the risk assessment. MyMap and/or Google Maps can be used to check receptors (residential houses, schools, public rights of way etc.)
Does the OMP describe methods for management of odorous material and/or odour specific mitigation measures?? |  | This could include: process controls, operating techniques, building design/containment, ventilation and abatement. Odours at each stage of the process should be considered.
Does the OMP include details of how they monitor odour emission or conditions which cause odour? Does this specify the parameters to be measured and trigger levels for corrective action?
Does the OMP include contingency measures and action plans to deal with accidents, emergencies and other abnormal events which may result in odour pollution? |  | Note that this may be contained within an Accidents Management Plan or similar.

## Dust and Bioaerosols
Dust Management Plan | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | Required where the installation is located within 100 metres of sensitive receptors or where an emission may pose a risk to the nearest sensitive receptors location. Required for new applications and variation to increase tonnage and/or change process. | Control and monitor emissions for your environmental permit - GOV.UK (www.gov.uk)
Does the DMP include a description of the site and operations?
Does the DMP include a site plan?
Does the DMP include details of local sensitive receptors?
Does the DMP detail the sources of dust emissions?
Does the DMP detail control methods?
Does the DMP detail the site abatement systems, including the nomination of responsibility?
Does the DMP include details on how complaints will be responded to?
Does the DMP provide details of the location and specification of site PM10 monitoring? |  | Details should include location of monitor, how the data in managed, how the equipment is serviced and calibrated and the trigger action levels (if applicable).
Bioaerosol Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | Required where the operational area is located within 250 metres of sensitive receptors or where an emission may pose a risk to the nearest sensitive receptors location. Required for new applications and variation to increase tonnage and/or change process. | Bioaerosol monitoring at regulated facilities - use of M9: RPS 209 - GOV.UK (www.gov.uk)
Has the risk assessment been completed in line with the relevant guidance?

## Pests
Pest Management Plans | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | Required if the risk assessment indicates the proposed operation is likely to cause pests. | Control and monitor emissions for your environmental permit - GOV.UK (www.gov.uk) | Natural Resources Wales / How to comply with your environmental permit
Is it sufficient? |  | Should clearly detail how pests will be prevented or minimised. See 'control and monitor your emissions' guidance for more information.

## Accidents and Containment
Accident Management Plans | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | All installation's require a written accident management plan to form part of their EMS. Use your judgement as to whether we need the full accident management plan submitted as part of the application for assessment. | Natural Resources Wales / How to comply with your environmental permit
Is it sufficient? |  | See guidance on what an accident management plan should include in 'How to comply'.
Flood Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
Has one been submitted if required? |  | Required if site is within a flood risk zone (check MyMap for Permitting). The assessment should assess risk of pollution in the event of flooding (note this is different to a Flood Consequence Assessment which assesses how a proposal may impact the frequency of flooding - this is covered by planning). Sometimes this is covered in the Accident Management Plan.
Is it sufficient?
Containment Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
Has a containment risk assessment been submitted if required? |  | Required where a proposal includes storage of liquids which could be harmful if released to ground and water. | Containment systems for the prevention of pollution (CIRIA C736)
Has the risk assessment been completed in line with the relevant guidance? |  | Assessment of primary, secondary and where relevant, tertiary containment measures following the source, pathway, receptor model as outline in 'Containment systems for the prevention of pollution' (CIRIA C736)
Alternative Measures Has the applicant proposed alternative measures to secondary containment? |  | I.e. use of tertiary containment or use of storage lagoons? These may be acceptable for purpose of duly making, however application must be accompanied with justification for alternative measures proposed, and evidence to confirm no impact pathway off site to surface waters / goundwaters
Have bund capacity calculations been included within asssessment? I.e. Capacity greater than 110 percent of the largest tank or 25 percent of the total tankage, whichever is the larger. |  | Must list ALL tanks to be located within bunded area - and present storage volumes for each tank along with calculations for storage capacity of secondary containment.
Does the assessment include a completed source, impact pathway receptor model to calculate level of containment required? I.e. Class 1; Class 2; or Class 3 containment required? |  | The applicant needs to clearly define the potential impact pathway and sensitivity of receptor. NB. For Anaerobic Digester sites we would accepted completed assessments using ADBA's risk assessment tool
Engineering design of structures in the containment system Have technical specifications / construction CQA plans / detailed design / elevation drawings (drawn to scale) been provided for the containment proposed? |  | Design and construction must be validated by a suitably qualified person (competent engineer) CQA reports for as-built (evidence built according to plan, competent engineer sign-off) - can be captured under pre-op condition
If yes, has evidence been provided to demonstrate that the design has been validated by a suitably qualified person?
Have details been provided of procedure for managing and removing clean uncontaminated surface water collected within the bunded area during normal operations? E.g. regular visual inspections - any contents must be pumped out or otherwise removed under manual control after checking for contamination.

## FPMP
Fire Prevention and Mitigation Plan (FPMP) | Yes / No / N/A | Comments / Guidance Notes | Links
Is the FPMP produced in accordance with NRW guidance? |  | Always required. | Guidance No. 16 Fire prevention and mitigation plan - waste management (naturalresources.wales)
Does the FPMP contain the following:
The amount and type of waste received daily and how it is managed. |  | Always required.
Total amount of waste and types and forms (e.g. unprocessed, shredded etc) stored on site at any one time and how it will be stored |  | Always required.
Maximum time each type of waste will be stored on site |  | Always required.
Maximum size of any waste stockpile - including length, width and depth
Minimum separation distances used |  | Always required.
Clear area around the perimeter |  | Always required.
Fire prevention techniques used, including management of hotspots, self combustion, monitoring, reporting |  | Always required.
Techniques used to minimise fire spreading |  | Always required.
All combustion products and emissions (to air, land and water) including impact on the local community, critical infrastructure and environment).
Contact details of sensitive receptors within 1km of the site, including human receptors (i.e. hospitals, residential areas, schools) |  | Always required.
Environmental receptors within 1km of the site (i.e. source protection, surface water) |  | Always required.
Has a site plan been provided showing the following: |  | Always required.
where each type of waste is stored |  | Always required.
layout of buildings |  | Always required.
areas where hazardous materials are stored (e.g. gas cylinders, oil and fuel tanks) |  | Always required.
main access route and any alternative access points |  | Always required.
location of hydrants and water supplies |  | Always required.
areas of natural and unmade ground |  | Always required.
location of plant, pollution control equipment |  | Always required.
drainage system, foul and surface water drains, their direction and outfall. |  | Always required.
location of drain covers and pollution control measures - e.g. firewater containment system |  | Always required.
location of sensitive receptors within 1km of the site including human receptors and environmental receptors. |  | Always required.
designated quarantine area |  | Always required.
Does the FPMP include a list of common causes of fires and preventative measures, as per the guidance?
If the waste is at risk of self combustion, and they are proposing to store for more than 3 months - are additional measures included? |  | Always required if relevant.
Does the FPMP include how End of Life Vehicles will be stored (if relevant)? |  | Always required if relevant.
Does the FPMP include how they are reducing the risk of fire occurring within baled waste storage (if relevant)? |  | Always required if relevant.
For enclosed stacks using bales and walls, do the bays or walls between the stacks provide fire resistance for 120 mins? Has evidence of product specification been included?
For wastes stored within a building, has the applicant included general principals on fire prevention and mitigation?
If waste is stored in containers, does the FPMP include how containers will be moved?
Does the FPMP include information on waste stack management, i.e. the contracts in place to ensure that they have end user outlets.
Does the FPMP include monitoring that will be carried out?
Does the FPMP explain what indicators will be used in relation to temperature and moisture content and what action will be taken in relation to these?
Does the FPMP include how they will detect fire in early stages?
If a fire suppression system is proposed, does the FPMP include what type of system it is?
Does the FPMP include heavy mobile plant available to move waste?
Does the FPMP include the suitability of the heavy plant?
Are trained staff available to move waste?
Has amount of water required for largest stack been calculated? |  | Always required.
Does the FPMP include where the water supply will come from? |  | Always required.
Have they included information to demonstrate the hydrant is suitable?
If using alternative sources (i.e. river) has information been included to support that this is a reliable source? |  | Always required.
Does the FPMP include measures to contain fire water run-off?
Does the FPMP include calculations to demonstrate how much water can be contained?
If firewater is being discharged to sewer, has evidence of approval from the sewage company been included?
Have measures to prevent firewater reaching groundwater and surface water been included?
Does the FPMP include a designated quarantine area? Does it include separation distances? Does it state how much waste it can contain? Is the quarantine area within the permitted boundary?
Does the FPMP include contingency measures during and after a fire? i.e. diverting waste, notifying those who may be affected. |  | Always required.
Does the FPMP include a plan to notify those who may be affected by the fire? |  | Always required.
Does the FPMP include how the site will be cleared and decontaminated after an incident? |  | Always required.
Does the FPMP include when it will be reviewed?

## Energy from Waste
Specific Questions relating to the Energy from Waste Sector | Yes / No / N/A | Comments / Guidance Notes | Links
Is it clear as to if the Applicant is proposing an incinerator or co-incinerator? |  |  | guidance-on-when-a-plant-is-a-co-incineration-plant.pdf (naturalresources.wales)
Is it clear as to if there is on-site pre-treatment? |  | Note that for Part A 5.1 plant pre-treatment is included in the activity provided the output from pre-treatment is dedicated to the incineration activity.
If Incinerator Bottom Ash treatment is proposed, has it been correctly identified? _ suff details.
Have the minimum preformance standards if IED chapter 4 been addressed? |  | A summary of how the Operating Techniques complies with IED chapter 4 requirements. Note that this is needed in addition to the BAT assessment.
Has a Human Health Risk Assessment been provided?
Does the Human Health Risk Assessment eference either the USEPA Human Health Risk Assessment Protocol or the HMIP 1996 report. |  |  | Human Health Risk Assessment ¦ US EPA
Does the Human Health Risk Assessment compare dioxin intake to the COT tolerable daily intake (TDI).
Does the Human Health Assessment include assessment of dioxin like PCBs?
Has an assessment of the options taking into account cost vs benefit for: - Furnace choice - Abatement options and reagent used - Cooling method - Options for recovering heat - Energy efficiency - Global warming potensial
Does the application include details on whether back up Continuous Emission Monitoring System (CEMS) will be available?
Does the application include details on sampling points and locations? |  |  | https://www.gov.uk/guidance/monitoring-stack-emissions-technical-guidance-for-selecting-a-monitoring-approach | technical-guidance-note-m1-monitoring-sampling-requirements-for-stack-emission-monitoring-saesneg-yn-unig.pdf (cyfoethnaturiol.cymru)
Where gasification or pyrolysis is proposed and the Applicant has claimed the syngas meets 'end of waste' and does not cause emissions higher than natural gas, have details on the syngas specification been provided and compared to natural gas? Has an end of waste application been submitted? If syngas is to be exported then end of waste requires defined markets to be demonstrated? |  | See linked guidance to aid comparison. Note that if syngas is to be exported then end of waste requires defined markets to be demonstrated. | Material comparators to assist in an end-of-waste assessment - GOV.UK (www.gov.uk)
Where gasification or pyrolysis is proposed has the Applicant confirmed char will meet 3% Total Organic Carbon (TOC) or 5% Loss on ignition (LOI)?
Where gasification or pyrolysis is proposed, does the application confim residues will be burned to generate energy? |  | if yes, emissions will be subject to IED Chapter IV.
If proposing to incinerate hazardous waste, have the requirements been met? |  | See EPR 5.01 for requirements on incinerating hazardous waste. | https://www.gov.uk/government/publications/incineration-of-waste-epr501-additional-guidance
Has the application provided a definition of start-up and shutdown conditions which defines when a plcant can commence charging or cease charging waste (and an alternative waste derived fuel) with compliance to co-incineration requirements)?

## Haz and Non-Haz Waste Treatment
14 | Specific Questions relating to the Non-Hazardous/Hazardous Waste Transfer and/or Treatment Sector (including leachate treatment plants and clinical waste) | Yes / No / N/A | Comments / Guidance Notes | Links
| Have the details of waste pre-acceptance and acceptance procedures been provided? |  | Note this might be included in the BAT Assessment / linked to specific BAT conclusions. Should include issues such as loads arriving, inspection, sampling, rejecting and keeping records. Procedures need to be line with Sector Guidance Note S5.06: recovery and disposal of hazardous and non-hazardous waste (see links). | Sector Guidance Note S5.06: recovery and disposal of hazardous and non-hazardous waste - GOV.UK (www.gov.uk) | How to comply with your environmental permit. Additional guidance for Clinical Waste (EPR 5.07)
| Have details of s of storage procedures and capacities been provided? |  | Note this might be included in the BAT Assessment . For Hazardous Waste facilities this should show separation/segregation for potentially incompatible wastes.
| Have details of the waste treatment methods and infrastructure been provided? |  | Note this might be included in the BAT Assessment.
| Has a suitable layout plan been provided? |  | Check this is suitably labelled to identify storage tanks/bays/areas by waste type and storage capacity.
Has a list of wastes (with EWC codes) for each of the storage/treatment activities applied for?
| Has proposed annual throughput been provided? |  | See application form Part B3 (or C3 for variations).

## Chemicals
Specific Questions relating to the Chemical sector | Yes / No / N/A | Comments / Guidance Notes | Links
Has a technical description of the activities been provided? |  | This should give us enough information to allow us to understand: - the prices - the main plant and equipment used for each process - all reactions, including significant side reactions (chemistry of the process) - the materials mass flows (including products and management systems) for situations which could involve a significant release of emissions - particularly the main reactions and how they are controlled Note this might be included in the BAT Assessment | Speciality organic chemicals sector: additional guidance - GOV.UK (www.gov.uk)
Has a description of the accident prevention and control measures been provided? |  | Note this might be detailed in a standalone 'Accident Risk Assessment' and 'Accident Management Plan' Larger risks are likely to be covered by COMAH Regulation requirements. However, the applicant must demonstrate that lesser risks are adequately controlled. The use of bulk storage vessels and liquid transfer via over ground pipework is likely in this sector. Therefore detailed assessment of containment measures; including surfacing, drainage, inspections and maintenance techniques will be required.
If a multi-purpose plant is proposed, has a 'Multi Product Protocol' been provided?

## Cement Lime and Minerals
Specific Questions relating to the Cement, Lime and Mineral sector | Yes / No / N/A | Comments / Guidance Notes | Links
If proposal is subject to Code of Practice - are the listed waste codes in line with current permits that contain the code of practice codes. For wastes proposed that are not contained within Code of Practice, has a detailed feasibility check been provided?
Has the application provided a definition of Kiln start-up and Kiln shutdown conditions which defines when a plant can commence charging or cease charging waste (and an alternative waste derived fuel) with compliance to co-incineration requirements)?
If the Applicant proposes to burn waste, has a full assessment of how the proposal will comply with the requirements of IED been provided? |  | For Cement Installation – IED sets mandatory ELVs. For Lime installations (burning waste) Pt 4 of Annex VI (IED) is appropriate to determine ELVs by mixing rule calculation. This includes human health risk assessment air quality risk assessment, details of monitoring (Continuous Emissions Monitoring - CEMS) etc. References to concentrations of substances in emissions into air means: (a) in relation to emissions from cement kilns, the concentration in dry air at a temperature of 273K, at a pressure of 101.3 kPa and with an oxygen content of 10% dry for all fuels; and (b) in relation to emissions from non-combustion sources, the concentration in dry air at a temperature of 273K, at a pressure of 101.3 kPa and with no correction required for oxygen.

## Combustion
Specific Questions relating to the Combustion sector (including Gas Utilisation Plants) | Yes / No / N/A | Comments / Guidance Notes | Links
Has the thermal input in megawatts (MW) for each combustion unit been specified? |  | The MWth is used to classify activities within the Environmental Permit Regulations (EPR): • <20MWth is likely to be considered a Directly Associated Activity and may be a Medium Combustion Plant (MCP) if >1MWth. • Individual units >20MWth should be checked against Part B & section 1.1 thresholds in EPR. • Aggregated units > 50MWth should be checked against section 1.1 thresholds in EPR. See guidance for more information. | Natural Resources Wales / Medium combustion plant and specified generator activities
If Medium Combustion Plant Directives (MCPD) apply, has all 'Annex 1' information been provided? |  | You should have been provided with enough information to determine if these regulations apply See Application Form Part B3, Appendix 8.
If Specified Generator Regulations apply has the applicant provided the relavent information? |  | See snapshot to the right for information we require
If the application includes a proposed peaking plant ("short term operating reserve" STOR) has the applicant applied for annual operation hours of less than 1500 (as a rolling average 2250 hours? |  | If not, speak to Lead Specialist Officer or sector lead for further advice. (This question relates to the requirement under the Energy Efficiency Directive to complete a cost-benefit analysis to determine whether it is feasible to utilise waste heat for combined heat and power and / or district heating. This requirement applies to combustion sites that are >20MW thermal input, except those which fall under exemptions listed in the EED, one of which is combustion sites that provide back-up power generation (which includes STOR and peaking plants) that operate for less than 1500 hours (and 2250 hours as a rolling average over 5 years.). From Article 14(5) of the Energy Efficiency Directive 2012/27/EU.
If the application includes a diesel array peaking plant only, has the applicant aggregated units of <1MWth?
If the application is for a data centre, has the Applicant clearly defined their maintenance scenario in terms of numbers of plants operating at any one time, duration and location of plant operation?
For Large Combustion Plants, does the application include information about the cooling system. If the cooling system will be water based has the thermal plume been considered?
For Large Combustion Plants propsing to burn biomass, does the application include what fuel types are proposed?
For variations, does the installation hold an exsisting Greenhouse Gas Permit? |  | Check exsisting list (under links) and notify the climate change team at GHGHelp@cyfoethnaturiolcymru.gov.uk to ask if as a result of their variation to their EPR permit do they need to vary their GHG permit. Advise the Operator accordingly. (Does not effect the duly making decision). | Exsisting installations permits which hold GHG permits

## Refinery
Specific Questions relating to the Refinery sector | Yes / No / N/A | Comments / Guidance Notes | Links
Has a Volatile Organic Compound (VOC ) Management Plan been submitted?

## Landfill
Specific Questions relating to the Landfill sector |  |  | Links
The linked Environment Agency guidance has not yet been formally adopted by NRW. Please speak to Lead Specialist Officer or sector lead if you have an landfill application to check applicability of guidance. |  |  | Landfill operators: environmental permits - Guidance - GOV.UK (www.gov.uk)
Environmental permitting: landfill sector technical guidance - GOV.UK (www.gov.uk)
Understanding the Landfill Directive LFD 1 (cyfoethnaturiol.cymru)
Financial Provision | Yes / No / N/A | Comments / Guidance Notes | Links
Has the Applicant confirmed how financial provision will be made and has an expenditure plan been submitted? |  | See Application Form B2, section 3c. The applicant needs to show they are financially capable of meeting the obligations of closure and aftercare. If this has not been provided and/or has not yet been arranged, we should not duly make the application. | Landfill operators: environmental permits - Calculate your financial provision - Guidance - GOV.UK (www.gov.uk)
Environmental Setting and Installation Design (ESID) Report | Yes / No / N/A | Comments / Guidance Notes | Links
if required, has one been provided? |  |  | Landfill operators: environmental permits - What to include in your environmental setting and site design report - Guidance - GOV.UK (www.gov.uk)
Does it include site details? |  | e.g. location, site context
Does it include compliance points? |  | e.g. Groundwater, surface water discharges
Does it include pollution control measures? |  | e.g. attenuation later (if sensitive location), drainage ditches, etc
Has monitoring been proposed? |  | e.g. gas monitoring if identified as required by risk assessment
Conceptual site model (CSM) | Yes / No / N/A | Comments / Guidance Notes | Links
if required, has a CSM been provided and does it meet the requirements set out in the guidance? |  | The ESID will be used to develop the CSM. The CSM will then feed into the required risk assessments. | Landfill operators: environmental permits - Plan the environmental setting of your site - Guidance - GOV.UK (www.gov.uk)
Drawings | Yes / No / N/A | Comments / Guidance Notes | Links
if required, have drawings been presented and do they include all the information we would expect? |  | These may be referenced in the CSM and/or HRA and will vary according to site specific circumstances.
Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
Has a generic Environmental Risk Assessment (ERA) been submitted? | Please refer to Risk Assessment tab on this spreadsheet which will also apply to landfills. Risk assessments and associated management plans for noise, odour, surface water, pests, dust etc may also apply. The Landfill Guidance provides further information on what risk assessments and management plans are required. Please see below for further checks for specific landfill risk assessments. |  | Landfill operators: environmental permits - Develop and maintain management plans - Guidance - GOV.UK (www.gov.uk)
Hydrogeological Risk Assessment (HRA) | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has one been submitted? |  | Required if a Conceptual Site Model (CSM) confirms site presents a risk to water. Can be Qualitative or Quantitative. Consider if the right type has been submitted. Quantitative assessments are required if it he activity is within a sensitive location i.e. on a principal aquifer / secondary A aquifer; below the water table; SPZ 2 & 3; or in an area where groundwater provides a direct pathway to other sensitive receptors e.g. habitat sites. We would be unlikely to grant an environmental permit for a DfR site in a SPZ 1. | Landfill operators: environmental permits - What to include in your hydrogeological risk assessment - Guidance - GOV.UK (www.gov.uk)
Does the HRA include all the sections outlined in the guidance?
Does the HRA include detail on site setting and CSM (or reference to it)?
Does the HRA suitable justify the level of assessment / modelling approach?
Does the HRA review: - natural geology - geological barrier - attenuation layer - surface water management system
Have details of proposed groundwater limits and monitoring been proposed? |  |  | pres 17 (publishing.service.gov.uk)
Stability Risk Assessment | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has one been submitted and is it sufficient? |  | Required if CSM confirms it is needed. | How to do a stability risk assessment for landfill sites of inert waste or deposit for recovery - GOV.UK (www.gov.uk) | Stability of landfill lining systems - GOV.UK (www.gov.uk)
Landfill Gas | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has a landfill gas risk assessment been submitted and is it sufficient? |  |  | LFTGN03: guidance on the management of landfill gas - GOV.UK (www.gov.uk)
Has the applicant provided sufficient detail on landfill gas extraction, limits and monitoring system based on the site-specific risk assessment? |  |  | Landfill operators: environmental permits - Manage landfill gas - Guidance - GOV.UK (www.gov.uk) | Landfill operators: environmental permits - Develop and maintain management plans - Guidance - GOV.UK (www.gov.uk)
If required, has a landfill gas management plan been submitted and is it sufficient?
Leachate | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has a leachate risk a assessment been submitted and is it sufficient? |  |  | Landfill developments: groundwater risk assessment for leachate - GOV.UK (www.gov.uk)
If the applicant is proposing to increase leachate levels, has all the required information, as detailed in the guidance, been provided? |  |  | Landfill operators: environmental permits - Manage leachate - Guidance - GOV.UK (www.gov.uk)
If required, has a leachate management plan been provided and is it sufficient? |  |  | Landfill operators: environmental permits - Develop and maintain management plans - Guidance - GOV.UK (www.gov.uk)
Landfill Design, Restoration and Closure | Yes / No / N/A | Comments / Guidance Notes | Links
Has the applicant provided sufficient detail for us to assess their landfill design? |  | Details on each relevant element of the landfill engineering and infrastructure for example (but not limited to) earthworks, geological barrier, leachate drainage and collection, leachate extraction and monitoring, landfill gas extraction and monitoring and landfill capping etc. See guidance for further information. | Landfill operators: environmental permits - Design and build your landfill site - Guidance - GOV.UK (www.gov.uk)
if required, has information on restoration been provided? |  |  | Landfill operators: environmental permits - Restore your landfill site - Guidance - GOV.UK (www.gov.uk)
If required, has information on closure been provided? |  |  | Landfill operators: environmental permits - Close your landfill site - Guidance - GOV.UK (www.gov.uk)
Waste Deposit | Yes / No / N/A | Comments / Guidance Notes | Links
Have details on waste acceptance been provided? |  |  | Landfill operators: environmental permits - Accept the right waste - Guidance - GOV.UK (www.gov.uk)
Has a full of EWC codes been provided?
Waste Recovery Plans (WRP) | Yes / No / N/A | Comments / Guidance Notes | Links
If required, has one been submitted? |  | Required for any proposal which proposes Waste Recovery as part of their operation (normally seen for the restoration phase) | Natural Resources Wales / Depositing waste for recovery
Check to see if the WRP has already been submitted for assessment by the Waste Permitting Team? |  | Contact the Waste Permitting Team. If they have assessed the WRP and confirmed it is suitable, no more further duly making checks are required.
Does the WRP include evidence to support recovery of waste? |  | Must demonstrate one of the following 3 options: 1. Financial gain or other worthwhile benefit by using non-waste materials 2 Funding to use non-waste materials 3. Specific or General Obligation
If demonstrating obligation through planning permission, has a copy of the planning permission been supplied?
Does the WMP include evidence that the waste is serving a useful purpose (is suitable)? |  | A full list of waste types and function they are fulfilling must be provided. Details on how the recovery waste is a suitable substitution for non-recovered waste should be provided.
If waste is being used to improve soil quality (e.g. land spreading), has a benefit statement been provided. |  | Improving soil quality is not the same as creating a soil profile, benefit statement is not required for creating a soil profile.
Does the WRP detail the purpose of the work? |  | Why it is needed and how it will meet that need. Note this is N/A if the WRP has evidenced 'specific obligation'
Does the WRP detail the quantity of waste proposed to be used? |  | This should include plans and cross sections. Note this is N/A if the WRP has evidence 'specific obligation'
Does the WRP detail how quality standards will be met? |  | Should show it is fit for purpose and completed scheme will not result in environmental problems/harm. Note this is N/A if the WRP has evidenced a 'specific obligation'