## Guidance - please read
Version | NRW V2.1 No Macros | Opra Scheme NRW V2.1 - 2023
This version of OPRA has been developed to work without any of the macros that were embedded in previous versions.
The guidance for Installations Opra for EPR: Annex A – Opra Scheme for Installations (publishing.service.gov.uk) (Click here for LINK) is still applicable for Installations in Wales, APART FROM the following rules which mainly apply to Chemical activities:
Rule 3 - The complexity cap part of this rule has been amended so that only activities with exactly the same complexity band will count towards the total for capping. For example, currently if a site has 5 organic chemical activities with the same 4.1 sub-reference, they will be counted together and capped at 3, regardless of whether they fall into <2000 TPA (complexity band B) or >2000 TPA (complexity band C). In this version of OPRA the different sized activities will be counted separately, so that might mean 3 activities >2000 TPA and 2 activities <2000TPA.
Rule 4 - This rule still applies but you will need to discuss how to aggregate your site's activities with your local NRW officer.
Rule 5 - has been removed. This relates to Chemical sites with a multi-product protocol.
Guidance on NRW's current charges can be found by searching for "Our charges" on the NRW website: Natural Resources Wales (Click here for LINK)
The Defra Core Guidance Environmental permitting guidance: Core guidance - GOV.UK (www.gov.uk) (Click here for LINK) is a useful source of information about interpretting the Environmental Permitting Regulations. It includes guidance about claiming commercial confidentiality if you think this is relevent for your activities.
Please note that OPRA is now only used for annual subsistence charges. You do still need to review your OPRA profile regularly to ensure that you are paying the correct charge

## Introduction
Version | NRW V2.2 No Macros |  |  |  |  | Opra Scheme NRW V2.2 -2024
Operational Risk Appraisal (Opra) for Installations under EPR
| Organisation Name | Tata Steel UK Limited |  |  |  | Permit Number |  | EPR/BL7108IM
| Date | 2025-05-01
It is recommended that the user fills in the spreadsheet following the order of worksheets listed below (click on the appropriate tab at the bottom of the screen). Not all worksheets require input, for those that do, the fields that may require input have no background colour or where there is a blue colour a picklist option is available. To move to the next data entry cell in a worksheet, press tab button once the first cell has been completed and you will go to the next unlocked cell where data or a picklist needs to be entered or completed. The sequence of worksheets is divided into two sections Sheets 1 to 11 are concerned with the input of data. Sheet 12 is the summary for the Opra Scores and Sheet 13 displays the charges.
| Colour coding | Free text | Pick List | Auto- populated | Guidance link available | Instruction | Cell answered | Information or commentary
| Does this document contain information that is commercial in confidence ? |  |  |  | No
Defra Core guidance
1 | Listed Activities |  |  |  | 7 | Emissions to Sewer
| Please refer to the Opra Scheme for Installations for the look-up tables and guidance. Use abbreviated descriptions, select the Schedule 1 references and bands from the pick lists provided. |  |  |  |  | Please enter details of your emissions to sewer on this sheet
[5 empty] | 8 | Emissions to Waste
Please enter details of waste taken off site, or imported for waste treatment activities
2 | Other Activities
| Please enter Part A(2), Part B, Medium Combustion Plant, Specified Generator and Waste Operation activities onto this sheet. These activities attract separate charges |  |  |  | 9 | Emissions Summary
No input is required. Output screen only. Summary of emissions.
3 | Complexities |  |  |  | 10 | Location
| Summary of complexities and rules applied - you only need to answer rule 6 on this worksheet |  |  |  |  | Please answer the questions regarding the location of your site on this sheet
[5 empty] | 11 | Operational Management
4 | Emissions to Air |  |  |  |  | Please answer the questions regarding your site management
| Please enter details of your emissions to air on this sheet |  |  |  | 12 | Opra Summary
5 | Emissions to Water |  |  |  |  | No input is required. Output screen only. The emissions are shown separately.
Please enter details of your emissions to water on this sheet
6 | Emissions to Land |  |  |  | 13 | Calculation
| Please enter details of your emissions to land on this sheet |  |  |  |  | No input is required. Charges with separate emissions totals.

## 1 Listed activity
Listed Activities - Complexity Attribute
|  | Organisation name: | Tata Steel UK Limited
|  | Permit Number: | EPR/BL7108IM
| Former Permit Ref (If applicable) | Description of Activity | Schedule 1 Reference | Regulatory Complexity |  | Totals before any rules are applied
| 1 | Reheat Furnace A (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C |  | A | 2
| 2 | Reheat Furnace B (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C |  | B | 2
| 3 | Hot Rolling Mill | 2.1 Part A (1) c) | C |  | C | 3
| 4 | Pickle Line | 2.3 Part A (1) a) | A |  | D | 0
| 5 | Aqueous effluent treatment | 5.3 Part A (1) a) (ii) | B |  | E | 0
| 6 | Cold Mill Effluent Treatment Plant | 5.3 Part A (1) a) (ii) | B
| 7 | HAA Waste Transfer and Treatment | 5.4 Part A (1) b) (iii) | A
8
9
10
11
12
13
14
15
16
17
| 18 |  |  |  |  | If there is insufficient space please attach a paper record
19
20
21
22
23
24
25
Schedule 1 Part A(1) - Rule 4 Aggregation Details (Chemical Industry only) Please contact your local NRW Industry Regulation Team if you need to use this rule
|  | Aggregation Group | Description | Schedule 1 Ref | Complexity
1
2
|  |  | Rule 4 | Not Applied

## 2 Other activities
Schedule1 Part A(2) and Part B Activities, Medium combustion plant, Specified generators and Directly Associated Waste Activities
Organisation Name: |  | Tata Steel UK Limited
Permit Number: |  | EPR/BL7108IM
These are activities that would require an Environmental Permit in their own right if they were not part of your Installation. They do not contribute to the OPRA score but incur separate charges. Listing each one here ensures we can charge the correct amount for any additional activities within the Installation.
List of EPR Schedule Part (A) 2, Part B, Medium Combustion Plant (MCP), Specified Generator (SG) and Directly Associated Waste Activities (DAA Waste) included in the Installation
| Enter description of Activity | Part A2 or Part B, MCP, SG or DAA Waste activity | EPR Schedule Reference
1 | Hired package boilers | MCP | Schedule 25A - Medium combustion plant only
2 | Coal and coke unloading and handling | PartB | 3.5 Part B b) iii)
3 | Yard Zero | DAA_Waste | Waste activity that is not a Part A(1) activity
4 | HAA Waste Transfer and Treatment | DAA_Waste | Waste activity that is not a Part A(1) activity
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20

## 3 Complexities
EPR- Installations Charging Scheme Complexity - Application of Rules
[13 empty] | Rule 6 | Rule 7
[13 empty] | This rule is applied if your site is >50Ha The first and highest complexity letter after any E will be increased by one - so a D would be come an E or a C would become a D or a B would become a C or an A would become a B | This rule is automatically applied if the number of complexities are >6. It drops the complexity by one band for the seventh and subsequent complexity scores
Organisation name |  | Tata Steel UK Limited |  |  | Rule 3 is applied when there are 4 or more of the identical Schedule reference and the same throughput band the complexity score is "*capped" | [7 empty] | Is the site >50 Ha? Please answer Y/N below
Permit number |  | EPR/BL7108IM | [10 empty] | Yes
| Complexities transferred from 1 Listed activities tab |  |  |  | Rule 3 capping applied but not sorted |  |  |  | Rule 3 applied and sorted
Former Permit Ref (if applicable) | Description / Aggregation Group | Schedule 1 Ref | Complexity |  | Description / Aggregation Group | Schedule 1 Ref | Complexity | capped Unsorted | Description / Aggregation Group | Schedule 1 Ref | Complexity | capped sorted | Rule 6 | Rule 7 | e | d | c | b | a
1 | Reheat Furnace A (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | 1 | HAA Waste Transfer and Treatment | 5.4 Part A (1) b) (iii) | A | A | Hot Rolling Mill | 2.1 Part A (1) c) | C | C | D | D | 0 | 0 | 1 | 0 | 0
2 | Reheat Furnace B (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | 2 | Aqueous effluent treatment | 5.3 Part A (1) a) (ii) | B | B | Reheat Furnace A (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | C | C | C | 0 | 0 | 2 | 0 | 0
3 | Hot Rolling Mill | 2.1 Part A (1) c) | C | 3 | Cold Mill Effluent Treatment Plant | 5.3 Part A (1) a) (ii) | B | B | Reheat Furnace B (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | C | C | C | 0 | 0 | 3 | 0 | 0
4 | Pickle Line | 2.3 Part A (1) a) | A | 4 | Pickle Line | 2.3 Part A (1) a) | A | A | Aqueous effluent treatment | 5.3 Part A (1) a) (ii) | B | B | B | B | 0 | 0 | 3 | 0 | 0
5 | Aqueous effluent treatment | 5.3 Part A (1) a) (ii) | B | 5 | Hot Rolling Mill | 2.1 Part A (1) c) | C | C | Cold Mill Effluent Treatment Plant | 5.3 Part A (1) a) (ii) | B | B | B | B | 0 | 0 | 3 | 0 | 0
6 | Cold Mill Effluent Treatment Plant | 5.3 Part A (1) a) (ii) | B | 6 | Reheat Furnace A (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | C | HAA Waste Transfer and Treatment | 5.4 Part A (1) b) (iii) | A | A | A | A | 0 | 0 | 3 | 0 | 1
7 | HAA Waste Transfer and Treatment | 5.4 Part A (1) b) (iii) | A | 7 | Reheat Furnace B (170 MW) | 1.1 Part A (1) a) (i) <300MW but >50MW | C | C | Pickle Line | 2.3 Part A (1) a) | A | A | A | A | 0 | 0 | 3 | 0 | 2
8 | 0 | 0 |  | 8 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
9 | 0 | 0 |  | 9 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
10 | 0 | 0 |  | 10 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
11 | 0 | 0 |  | 11 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
12 | 0 | 0 |  | 12 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
13 | 0 | 0 |  | 13 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
14 | 0 | 0 |  | 14 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
15 | 0 | 0 |  | 15 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
16 | 0 | 0 |  | 16 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
17 | 0 | 0 |  | 17 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
18 | 0 | 0 |  | 18 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
19 | 0 | 0 |  | 19 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
20 | 0 | 0 |  | 20 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
21 | 0 | 0 |  | 21 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
22 | 0 | 0 |  | 22 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
23 | 0 | 0 |  | 23 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
24 | 0 | 0 |  | 24 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
25 | 0 | 0 |  | 25 | 0 | 0 |  |  | 0 | 0 |  |  |  |  | 0 | 0 | 3 | 0 | 2
26 |  |  |  | 26 | 0 | 0 | 0 |  | 0 | 0 | 0 |  |  |  | 0 | 0 | 3 | 0 | 2
27 |  |  |  | 27 | 0 | 0 | 0 |  | 0 | 0 | 0 |  |  |  | 0 | 0 | 3 | 0 | 2
28 |  |  |  | 28 | 0 | 0 | 0 |  | 0 | 0 | 0 |  |  |  | 0 | 0 | 3 | 0 | 2
29 |  |  |  | 29 | 0 | 0 | 0 |  | 0 | 0 | 0 |  |  |  | 0 | 0 | 3 | 0 | 2
30 |  |  |  | 30 | 0 | 0 | 0 |  | 0 | 0 | 0 |  |  |  | 0 | 0 | 3 | 0 | 2
| Summary of Rules Applied |  | Status | These totals will be carried forward and used to calculate the Opra Risk Summary and Calculation of Charges
| Rule 3 | no
| Rule 4 | No
| Rule 5 | N/A
| Rule 6 | Yes | Complete
| Rule 7 | Yes
| Scores after Rules applied (Used for calculation of Charges) |  |  |  | Scores before rules applied (Used for summary of Risk)
Complexity | First 6 Complexities | Remaining complexities | Total
A | 1 | 1 | 2 |  | 2
B | 2 | 0 | 2 |  | 2
C | 2 | 0 | 2 |  | 3
D | 1 | 0 | 1 |  | 0
E | 0 | 0 | 0 |  | 0
*Capped | 0 | 0 | 0
You only need to answer the question about the size of your site on this page.
All the tables below are for information only to show how any relevant rules are applied.

## 4 Air
Emissions Attribute - Releases to Air
Organisation Name: | Tata Steel UK Limited |  |  |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
Permit Number: | EPR/BL7108IM
Please tick box if this sheet is applicable
Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
Oxides of Sulphur | Tonnes Year | 10 |  | 0
Oxides of Nitrogen | Tonnes Year | 10 | 5601 | 560.1 | Based on maximum firing rate 24 hours/day, 365 days/year, and emissions at 1,800 mg/Nm³.
Carbon Monoxide | Tonnes Year | 1000 |  | 0
Beryllium | Kg year | 1 |  | 0
Cadmium | Kg year | 1 |  | 0
Lead | Kg year | 1 |  | 0
Mercury | Kg year | 1 |  | 0
Antimony | Kg year | 10 |  | 0
Arsenic | Kg year | 10 |  | 0
Chromium | Kg year | 10 |  | 0
Nickel | Kg year | 10 |  | 0
Selenium | Kg year | 10 |  | 0
Other Metals Specify
| Kg year | 100 |  | 0
| Kg year | 100 |  | 0
| Kg year | 100 |  | 0
| Kg year | 100 |  | 0
| Kg year | 100 |  | 0
Organic Compounds
Dioxins and Furans | mg TEQ year | 0.1 |  | 0
PCBs | mg TEF year | 0.1 |  | 0
PAHs as benzo(a)pyrene | Kg year | 1 |  | 0
Phosgene | Kg year | 1 |  | 0
Isocyanates | Kg year | 1 |  | 0
Di-ethyl sulphate | Kg year | 1 |  | 0
Di-methyl sulphate | Kg year | 1 |  | 0
Acrylonitrile | Kg year | 10 |  | 0
Aniline | Kg year | 10 |  | 0
Benzene | Kg year | 10 |  | 0
Benzyl Chloride | Kg year | 10 |  | 0
1-chloro-2,3-epoxypropane | Kg year | 10 |  | 0
Chloroform | Kg year | 10 |  | 0
Cyanamide | Kg year | 10 |  | 0
Ethylene oxide | Kg year | 10 |  | 0
Formaldehyde | Kg year | 10 |  | 0
Maleic anhydride | Kg year | 10 |  | 0
Nitrobenzene | Kg year | 10 |  | 0
Allyl alcohol | Kg year | 10 |  | 0
Acetaldehyde | Kg year | 100 |  | 0
Acetonitrile | Kg year | 100 |  | 0
Benzene-1,2,4-tricarboxylic acid,1,2-anhydride | Kg year | 100 |  | 0
1,3-butadiene | Kg year | 100 |  | 0
Chloroethene | Kg year | 100 |  | 0
1,2-dichloroethane | Kg year | 100 |  | 0
Dimethylformamide | Kg year | 100 |  | 0
1,4-dioxane | Kg year | 100 |  | 0
2-ethyoxyethanol | Kg year | 100 |  | 0
2-ethyoxyethylecetate | Kg year | 100 |  | 0
Ethyl acrylate | Kg year | 100 |  | 0
Iodomethane | Kg year | 100 |  | 0
Methylamine | Kg year | 100 |  | 0
2-nitropropane | Kg year | 100 |  | 0
Phenol | Kg year | 100 |  | 0
Propylene oxide | Kg year | 100 |  | 0
HFC's | Kg year | 100 |  | 0
HCFC's | Kg year | 100 |  | 0
PFC's | Kg year | 100 |  | 0
Kg year
Benzaldehyde | Kg year | 500 |  | 0
Benzo(a)pyrene | Kg year | 500 |  | 0
Butene | Kg year | 500 |  | 0
Chloromethane | Kg year | 500 |  | 0
1,4-dichlorobenzene | Kg year | 500 |  | 0
Dichloromethane | Kg year | 500 |  | 0
Ethyl toluene | Kg year | 500 |  | 0
Ethylene | Kg year | 500 |  | 0
i-butyraldehyde | Kg year | 500 |  | 0
Methyl bromide | Kg year | 500 |  | 0
Pentene | Kg year | 500 |  | 0
Propene | Kg year | 500 |  | 0
Styrene | Kg year | 500 |  | 0
Tetrachloroethane | Kg year | 500 |  | 0
Tetrachloroethene | Kg year | 500 |  | 0
Toluene diamine | Kg year | 500 |  | 0
1,1,1-trichloroethane | Kg year | 500 |  | 0
Trichloroethylene | Kg year | 500 |  | 0
Trichlorotoluene | Kg year | 500 |  | 0
Trimethylbenzene | Kg year | 500 |  | 0
Xylene | Kg year | 500 |  | 0
Other VOCs specify
| Kg year | 1000 |  | 0
| Kg year | 1000 |  | 0
| Kg year | 1000 |  | 0
| Kg year | 1000 |  | 0
| Kg year | 1000 |  | 0
Inorganics
Fluorine | Kg year | 10 |  | 0
Chlorine | Kg year | 10 |  | 0
Bromine | Kg year | 10 |  | 0
Iodine | Kg year | 10 |  | 0
Hydrogen Fluoride | Kg year | 10 |  | 0
Hydrogen Bromide | Kg year | 10 |  | 0
Hydrogen Iodide | Kg year | 10 |  | 0
Hydrogen Chloride | Kg year | 1000 |  | 0
Hydrogen Sulphide | Kg year | 10 |  | 0
Ammonia | Kg year | 100 |  | 0
Carbon Disulphide | Kg year | 100 |  | 0
Particulates | Kg year | 100 |  | 0
Other inorganic compounds specify
Table A1 Substances | Kg year | 0.1 |  | 0
Table A2 Substances | Kg year | 1 |  | 0
Table A3 Substances | Kg year | 10 |  | 0
Table A4 Substances | Kg year | 100 |  | 0
Table A5 Substances | Kg year | 1000 |  | 0
Commercial in Confidence If you need to use these entries please contact your local NRW office
0
0
0
0
|  |  | Total | 560.1
Note on C118: The EA will publish, on its web site, thresholds for certain additional substances that may be released to air. In each case substances will be placed into tables with fixed release thresholds, as shown below.

## 5 Water
Emissions Attribute - Releases to Water
Organisation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
Permit Number: | EPR/BL7108IM
Please tick box if this sheet is applicable
Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
Aldrin | Kg year | 0.001 |  | 0
Azinphos-ethyl | Kg year | 0.001 |  | 0
DDT all isomers | Kg year | 0.001 |  | 0
Endosulfan | Kg year | 0.001 |  | 0
Endrin | Kg year | 0.001 |  | 0
Fenitrothion | Kg year | 0.001 |  | 0
Fenthion | Kg year | 0.001 |  | 0
Isodrin | Kg year | 0.001 |  | 0
Malathion | Kg year | 0.001 |  | 0
Parathion | Kg year | 0.001 |  | 0
Azinphos-methyl | Kg year | 0.01 |  | 0
Chlorfenvinphos | Kg year | 0.01 |  | 0
Diazinon | Kg year | 0.01 |  | 0
Dieldrin | Kg year | 0.01 |  | 0
Hexachlorobenzene | Kg year | 0.01 |  | 0
Hexachlorocyclohexanes | Kg year | 0.01 |  | 0
Hexachlorobutadiene | Kg year | 0.01 |  | 0
Mevinphos | Kg year | 0.01 |  | 0
Omethoate | Kg year | 0.01 |  | 0
Parathion methyl | Kg year | 0.01 |  | 0
Permethrin | Kg year | 0.01 |  | 0
Polychlorinated biphenyls | Kg year | 0.01 |  | 0
Triazophos | Kg year | 0.01 |  | 0
Tributyltin compounds | Kg year | 0.01 |  | 0
Trifluralin | Kg year | 0.01 |  | 0
Triphenyltin compounds | Kg year | 0.01 |  | 0
Atrazin | Kg year | 0.1 |  | 0
Pentachlorophenol and its compound | Kg year | 0.1 |  | 0
Simazine | Kg year | 0.1 |  | 0
Trichlorobenzene all isomers | Kg year | 0.1 |  | 0
Kg year
Benzene | Kg year | 1 |  | 0
Bentazone | Kg year | 1 |  | 0
Biphenyl | Kg year | 1 |  | 0
Carbon Tetrachloride | Kg year | 1 |  | 0
Chloroform | Kg year | 1 |  | 0
Chloronitrotoluenes | Kg year | 1 |  | 0
4-Chloro-3-Methylphenol | Kg year | 1 |  | 0
2-Chlorophenol | Kg year | 1 |  | 0
2,4 D non-ester | Kg year | 1 |  | 0
2,4 D ester | Kg year | 1 |  | 0
Demeton | Kg year | 1 |  | 0
1,2-Dichloroethane | Kg year | 1 |  | 0
Dimethoate | Kg year | 1 |  | 0
Linuron | Kg year | 1 |  | 0
Mecoprop | Kg year | 1 |  | 0
Napthalene | Kg year | 1 |  | 0
Tetrachloroethylene | Kg year | 1 |  | 0
1,1,1-Trichloroethane | Kg year | 1 |  | 0
1,1,2-Trichloroethane | Kg year | 1 |  | 0
Cadmium | Kg year | 1 | 56.7 | 56.7
Mercury | Kg year | 1 | 45.3 | 45.3
Nonylphenol Ethoxylate | Kg year | 20 |  | 0
Nonylphenols | Kg year | 20 |  | 0
Octylphenols | Kg year | 20 |  | 0
Toluene | Kg year | 20 |  | 0
Trichloroethylene | Kg year | 20 |  | 0
Xylenes | Kg year | 20 |  | 0
Arsenic | Kg year | 20 | 56.7 | 2.835
Chromium | Kg year | 20 | 144.9 | 7.245
Copper | Kg year | 20 | 179.9 | 8.995
Lead | Kg year | 20 | 430 | 21.5
Nickel | Kg year | 20 | 165.5 | 8.275
Zinc | Kg year | 20 | 28455.4 | 1422.77
All consented substances not listed above specify
Table W1 Substances | Kg year | 0.01 |  | 0
Table W2 Substances | Kg year | 0.1 |  | 0
Table W3 Substances | Kg year | 1 |  | 0
Table W4 Substances | Kg year | 20 |  | 0
Table W5 Substances | Kg year | 100 |  | 0
| Kg year |  |  | 0
| Kg year |  |  | 0
| Kg year |  |  | 0
Commercial in Confidence If you need to use these entries please contact your local NRW office
0
0
0
0
|  |  | Total | 1573.62
Note on B77: Please contact NRW for information on thresholds for certain additional substances that may be released to water. In each case substances will be placed into tables with fixed release thresholds, as shown below

## 6 Land
Emissions Attribute Releases to Land
| Organisation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
| Permit Number: | EPR/BL7108IM
Please tick box if this sheet is applicable
| Substance/Landfill Type | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
| Inert waste | Tonnes year | 1000 | 1660 | 1.66 | Ferric hydroxide filter cake. Estimate from October 2024 to March 2025, doubled to reflect annual emissions.
| Non hazardous waste (non biodegradable) | Tonnes year | 350 |  | 0
| Hazardous waste | Tonnes year | 100 |  | 0
| Non hazardous waste (biodegradable) | Tonnes year | 100 | 2881 | 28.81 | Mostly general refuse. Estimate from October 2024 to March 2025, doubled to reflect annual emissions.
|  |  |  | Total | 30.47

## 7 Sewer
Emissions Attribute - Off-site Disposals to Sewer
| Organisation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units.The Emission Index will only show if the data entered exceeds the threshold.
| Permit number: | EPR/BL7108IM
Please tick box if this sheet is applicable
| Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
| Aldrin | Kg year | 0.001 |  | 0
| Azinphos-ethyl | Kg year | 0.001 |  | 0
| DDT all isomers | Kg year | 0.001 |  | 0
| Endosulfan | Kg year | 0.001 |  | 0
| Endrin | Kg year | 0.001 |  | 0
| Fenitrothion | Kg year | 0.001 |  | 0
| Fenthion | Kg year | 0.001 |  | 0
| Isodrin | Kg year | 0.001 |  | 0
| Malathion | Kg year | 0.001 |  | 0
| Parathion | Kg year | 0.001 |  | 0
Kg year
| Azinphos-methyl | Kg year | 0.01 |  | 0
| chlorfenvinphos | Kg year | 0.01 |  | 0
| Diazinon | Kg year | 0.01 |  | 0
| Dieldrin | Kg year | 0.01 |  | 0
| Hexachlorobenzene | Kg year | 0.01 |  | 0
| Hexachlorocyclohexanes | Kg year | 0.01 |  | 0
| Hexachlorobutadiene | Kg year | 0.01 |  | 0
| Mevinphos | Kg year | 0.01 |  | 0
| Omethoate | Kg year | 0.01 |  | 0
| Parathion methyl | Kg year | 0.01 |  | 0
| Permethrin | Kg year | 0.01 |  | 0
| Polychlorinated biphenyls | Kg year | 0.01 |  | 0
| Triazophos | Kg year | 0.01 |  | 0
| Tributyltin compounds | Kg year | 0.01 |  | 0
| Trifluralin | Kg year | 0.01 |  | 0
| Triphenyltin compounds | Kg year | 0.01 |  | 0
| Atrazin | Kg year | 0.1 |  | 0
| Pentachlorophenol and its compound | Kg year | 0.1 |  | 0
| Simazine | Kg year | 0.1 |  | 0
| Trichlorobenzene all isomers | Kg year | 0.1 |  | 0
| Benzene | Kg year | 1 |  | 0
| Bentazone | Kg year | 1 |  | 0
| Biphenyl | Kg year | 1 |  | 0
| Carbon Tetrachloride | Kg year | 1 |  | 0
| Chloroform | Kg year | 1 |  | 0
| Chloronitrotoluenes | Kg year | 1 |  | 0
| 4-Chloro-3-Methylphenol | Kg year | 1 |  | 0
| 2-Chlorophenol | Kg year | 1 |  | 0
| 2,4 D non-ester | Kg year | 1 |  | 0
| 2,4 D ester | Kg year | 1 |  | 0
| Demeton | Kg year | 1 |  | 0
| 1,2-Dichloroethane | Kg year | 1 |  | 0
| Dimethoate | Kg year | 1 |  | 0
| Linuron | Kg year | 1 |  | 0
| Mecoprop | Kg year | 1 |  | 0
| Napthalene | Kg year | 1 |  | 0
| Tetrachloroethylene | Kg year | 1 |  | 0
| 1,1,1-Trichloroethane | Kg year | 1 |  | 0
| 1,1,2-Trichloroethane | Kg year | 1 |  | 0
| Cadmium | Kg year | 1 |  | 0
| Mercury | Kg year | 1 |  | 0
| Nonylphenol Ethoxylate | Kg year | 20 |  | 0
| Nonylphenols | Kg year | 20 |  | 0
| Octylphenols | Kg year | 20 |  | 0
| Toluene | Kg year | 20 |  | 0
| Trichloroethylene | Kg year | 20 |  | 0
| Xylenes | Kg year | 20 |  | 0
| Arsenic | Kg year | 20 |  | 0
| Chromium | Kg year | 20 |  | 0
| Copper | Kg year | 20 |  | 0
| Lead | Kg year | 20 |  | 0
| Nickel | Kg year | 20 |  | 0
| Zinc | Kg year | 20 |  | 0
All consented substances not listed above specify
| Chemical Oxygen Demand | Kg year | 10000 |  | 0
| Suspended Solids | Kg year | 10000 |  | 0
| Table S1 Substances | Kg year | 0.01 |  | 0
| Table S2 Substances | Kg year | 0.1 |  | 0
| Table S3 Substances | Kg year | 1 |  | 0
| Table S4 Substances | Kg year | 20 |  | 0
| Table S5 Substances | Kg year | 100 |  | 0
|  | Kg year |  |  | 0
Commercial in Confidence If you need to use these entries please contact your local NRW office
0
0
0
0
|  |  | Total |  | 0
|  |  | Weighting Factor |  | 0.33 | (Weighting factor = 0.33)
|  |  | Weighted Total |  | 0
Note on C76: The EA will publish, on its web site, thresholds for certain additional substances that may be released to sewer. In each case substances will be placed into tables with fixed release thresholds, as shown below.

## 8 Waste
Emissions Attribute - Off-site Disposals of Waste
| Organisation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
| Permit Number: | EPR/BL7108IM
| Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
| Inert waste | Tonnes year | 1000 |  | 0
| Non hazardous waste (non biodegradable) | Tonnes year | 350 |  | 0
| Hazardous waste | Tonnes year | 100 | 100 | 1 | Waste oil sent for incineration
| Non hazardous waste (biodegradable) | Tonnes year | 100 |  | 0
|  |  | Total |  | 1
|  |  | Weighting Factor |  | 0.33 | (Weighting factor = 0.33)
|  |  | Weighted Total |  | 0.33
Emissions Attribute - Off-site Recovery, Recycling, Re-use of Waste
| Installation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
| Permit Number: | EPR/BL7108IM
| Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
| Inert waste | Tonnes year | 1000 |  | 0
| Non hazardous waste (non biodegradable) | Tonnes year | 350 | 116113 | 331.7514 | Steel scrap sent for recovery
| Hazardous waste | Tonnes year | 100 | 280 | 2.8 | Oil pre-processed through Million Gallon Tank and sent for further recovery off-site
| Non hazardous waste (biodegradable) | Tonnes year | 100 |  | 0
|  |  | Total |  | 334.5514
|  |  | Weighting Factor |  | 0.1 | (Weighting factor = 0.1)
|  |  | Weighted Total |  | 33.4551
|  |  | Off-Site Total |  | 33.7851
The table below should only be completed for S5.3 or 5.4 activities. For these activities the Off-Site Waste tables above should be left blank
Emissions Attribute - Waste Input
| Installation Name: | Tata Steel UK Limited |  | Please check that the data is entered in the correct units. The Emission Index will only show if the data entered exceeds the threshold.
| Permit Number: | EPR/BL7108IM
| Substance | Units | Emission Threshold | Maximum Quantity | Emission Index | Notes
| Inert waste | Tonnes year | 1000 |  | 0
| Non hazardous waste (non biodegradable) | Tonnes year | 750 | 410000 | 546.6667 | Based on 350,000 tonnes per annum permitted for treatment at HAA and 60,000 tonnes per annum at Yard Zero.
| Hazardous waste | Tonnes year | 250 |  | 0
| Non hazardous waste (biodegradable) | Tonnes year | 500 |  | 0
|  |  | Waste Input Total |  | 546.6667

## 9 Emissions summary
Emissions Attribute Summary Sheet
| Organisation name | Tata Steel UK Limited
| Permit Number: | EPR/BL7108IM
| Pathway | Overall Emission Index
| Air | 560
| Water | 1574
| Land | 30
| Sewer | 0
| Waste Off Site | 34
| Waste Input | 547
| Pathway | Band
| Air | 3 | C
| Water | 4 | D
| Land | 2 | B
| Sewer | 0 | -
| Waste Off Site | 2 | B
| Waste Input | 3 | C

## 10 Location
Location Attribute
| Organisation Name: | Tata Steel UK Limited
| Permit Number: | EPR/BL7108IM
| Parameter | Yes/No | Available | Score
| Human Occupation/Presence: |  |  | 5
| a) if within 50m of the boundary | Yes | 5
or:
| b) if greater than 50m but less than 250m of boundary |  | 3
or:
| c) if greater than 250m but less than 1km of boundary |  | 1
| If your installation is within a certain distance of Statutory sites designated under Habitats Directive or CROW Act 2000 then the impact of emissions on these conservation areas must be assessed during our determination : |  |  | 3
| a) if "relevant" under Habitats Directive | Yes | 3
or
| b) if CROW Act 2000 assessment required |  | 2
| a) if on an aquifer and within a Groundwater Protection Zone |  | 2 | 1
or
| b) if on an aquifer and not within a Groundwater Protection Zone | Yes | 1
| Sensitivity of receiving waters (information available from the NRW web site see river basin management plans), if: | see Natural Resources Wales / River basin management plans 2015-2021 |  | 3
| a) WFD 'Bad' classification (formerly grade 5 ) |  | 1
| b) WFD 'Poor' or 'moderate' (previously grade 4 or 3) |  | 2
| c) WFD 'Good' or 'high' (previously grade 2 or 1) or estuarine | Yes | 3
| a) If there is direct runoff from the site without interceptors or other active control measures |  |  | 2
|  | Yes | 2
or
| b) If as above but there are interceptors or active control measures |  | 1
| a) If within an Air Quality Management Zone (AQMZ) and emit |  |  | 3
| pollutant that has been declared for that AQMZ | Yes | 3
or
b) If within 2km of an Air Quality Management Zone (AQMZ) and emit
| pollutant that has been declared for that AQMZ |  | 2 | 0
or
| c) as a) except do not emit pollutants that have be declared for the |  | 1
AQMZ
| If within a flood plain | Yes | 2 | 2
| Maximum Score = 20 Band A = 0 - 4, B = 5 - 8, C = 9 - 12, D = 13 - 17 and E = 18 - 20 | Total |  | 19
|  | Band |  | E
| Location attribute | Status
| Occupation | Complete
| Habitats | Complete
| Aquifers | Complete
| Receiving waters | Complete
| Run off | Complete
| Air Quality | Complete
| Flood plain | Complete
| Location Attribute Totals | Score
| Occupation | 5
| Habitats | 3
| Aquifers | 1
| Receiving Waters | 3
| Run Off | 2
| Air Quality | 3
| Flood Plain | 2

## 11 Operator performance
| Organisation Name: | Tata Steel UK Limited
| Permit Number: | EPR/BL7108IM
Operator Performance
|  | Yes/No | Points available | Points scored | Post or group responsible for each requirement |  | Document reference (*) or date by which systems will be in place (*see para 4.4.2)
Operations and Maintenance section - 20%
Effective operational and prev maintenance systems shall be employed on all aspects of the process where any failure could impact on the environment.
1 | Are there documented operating procedures for operations that may have an adverse impact on the environment? | Yes | 2 | 2
2 | Is there a defined procedure for identifying, reviewing and prioritising items of plant for which a preventative maintenance regime is appropriate? | Yes | 2 | 2
3 | Are there documented procedures for monitoring emissions or impacts? | Yes | 2 | 2
4 | Is there a preventative maintenance programme for those items of plant whose failure could lead to impact on the environment? | Yes | 1 | 1
5 | Does the preventative maintenance programme include regular checks and formal inspections of 'static' items such as tanks, pipework, retaining walls, bunds and ducts? | Yes | 1 | 1
6 | Do the operations and maintenance systems include auditing environmental performance? | Yes | 2 | 2
7 | Are the reports, results and recommendations arising from audits made available to senior management on a regular basis? | Yes | 2 | 2
8 | In the last two years, has there been any notifiable incident or release for which lack of maintenance was a contributory cause ? | Yes | -2 | -2
9 | In the last two years, has there been any notifiable incident or release for which the root cause could not be identified? | Yes | -3 | -3
| Operations and Maintenance Total |  | 12 | 7 | 58.33%
Competence and Training - 20%
The Operator shall ensure that all relevant management and operational staff (including contractors and those responsible for purchasing equipment and materials) receive adequate training with regard to their responsibilities under the Permit. Particular attention should be given to the following:
 Minimisation of all potential environmental effects from operation under normal, abnormal, start up and shut down circumstances;
 Prevention of accidental emissions and action to be taken when accidental emissions occur; and
 The need to report deviation from the permit.
1 | Has a training needs assessment been carried out which: | Yes | 3 | 3
 Identifies all posts for which specific environmental awareness training is required; and  Identifies the scope and level to which such training is to be given?
2 | Are training systems in place for all relevant staff that cover the following factors:
|  the regulatory requirements associated with the Permit as they affect their work activities and responsibilities; | Yes | 2 | 2
|  likely potential environmental impacts which may be caused by plant under their control. This should cover both normal and abnormal circumstances; | Yes | 2 | 2
|  reporting procedures to inform supervisors or managers of deviations from permit conditions; | Yes | 1 | 1
|  procedures to be used by supervisors or managers and for the reporting of deviations from permit conditions to Natural Resources Wales and | Yes | 2 | 2
|  prevention of accidental emissions and action to be taken when accidental emissions occur? | Yes | 2 | 2
3 | Are the skills and competencies necessary for key posts documented and are records of training needs and training received maintained? | Yes | 1 | 1
4 | Do the key posts include contractors, those responsible for liaising with contractors and those purchasing equipment and materials? | Yes | 1 | 1
5 | Do you assess the potential environmental risks posed by the work of contractors and provide instructions to contractors about protecting the environment while working on site? | Yes | 1 | 1
6 | In the last 2 years, have there been any notifiable incidents or releases, which it has been identified that lack of training was a contributory cause ? | No | -2 | 0
7 | Are there industry standards for training in this sector (e.g. WAMITAB) and if so do you apply them? (If no industry standards please use N/A) | Yes | -2 | 0
8 | Are individual and organisational training needs reviewed on a regular (e.g. annual) basis? | Yes | 2 | 2
| Competance Training Total |  | 17 | 17 | 100%
Emergency planning - 20%
The Operator shall maintain an accident management plan which identifies potential events or failures which might lead to an environmental impact. The plan shall identify:
 the likelihood of, and the actions to be taken to minimise, these potential occurrences;
 the environmental consequences and an action plan to deal with such occurrences;
 The Operator shall have a written procedure for handling, investigating, communicating and reporting of incidents and actual or potential non-compliance with permit conditions including taking action to mitigate any impacts caused and for initiating and completing corrective action.  In the case of abnormal emissions the operator shall;
 investigate and undertake remedial action immediately;
 promptly record the events and actions taken; and
 ensure the Regulator is made aware, as soon as practicable.
1 | Is there an accident plan that complies with guidance covering the following aspects of foreseeable scenarios: likelihood, consequences,actions to prevent, action to take in the event it occurs? | Yes | 4 | 4
2 | Has the plan identified areas where improvement is needed? | Yes | 1 | 0
2.1 | Where improvement has been identified, does the plan include an implementation programme with acceptable timescales to Natural Resources Wales (NRW)? If the plan is not acceptable to NRW, 2 points will be deducted. | Yes | -2 | 0
3 | Are there written procedures for handling, investigating, communicating and reporting actual or potential non compliance with operating procedures or emission limits? | Yes | 1 | 1
4 | Are there written procedures for handling, investigating, communicating and reporting environmental complaints? | Yes | 1 | 1
5 | Are there written procedures for investigating incidents, (and near-misses) including identifying suitable corrective action and following up implementation of that action? | Yes | 2 | 2
6 | In the last 2 years, have there been any notifiable incidents or releases for which it has been identified that lack of emergency planning was a contributory cause ? | No | -2 | 0
7 | Are there audit records of investigations into non compliance, complaints and incidents? Does the audit cover follow up actions? Do the audit reports go to senior managers? | Yes | 3 | 3
| Emergency planning Total |  | 12 | 11 | 91.67%
Organisation - 40%
If you operate under an externally auditted environment management system answer questions 1, 3 and 4, if you do not have an externally auditted environment management system answer questions 2, 3 and 4.
The following aspects of site management procedures and controls may not be in the permit conditions but are likely to have an impact on NRW resources required to apply the Env Permitting Regulations.
1 | Do you operate an externally audited environment management system, if so answer one of the following questions. N.B Please enter your Certificate Number, Name of certification body and their UKAS Registration Number in the space for document reference.
1.1 | Is your Environmental Management System EMAS registered? If yes select Yes and go to question 4. | No | 20 | 0 |  |  |  | complete
1.2 | Is your Environmental Management System certified to ISO 14001? If yes enter Yes and go to questions 3 and 4. | Yes | 15 | 15 |  |  | EMS Certificate No. GB98/13721 Certification Body SGS (UKAS Registration No. 0005) | complete | Enter details of your EMS certifcate number, certification body and their UKAS registration number into cell I66
1.3 | Is your system an Environmental Management System subject to external audit through a third party audit programme with a published methodology (excludes in-house company audit programme). If yes enter Yes and go to questions 3 and 4. | No | 12 | 0 |  |  | EMS Certificate No. GB98/13721 Certification Body SGS (UKAS Registration No. 0005) | complete
| Sub Total |  | 20 | 15 | 75% |  | Maximum score possible =20
2 | If you do not operate an externally audited environmental management system then assess your system against the criteria below:
2.1 | Has your company adopted an environmental policy and programme which :
|  includes a commitment to continual improvement and prevention of pollution? |  | 1 | 0 |  |  | Available upon request | complete
|  includes a commitment to comply with relevant legislation, and with other requirements that the organisation subscribes to? |  | 1 | 0 |  |  | Available upon request | complete
|  identifies, sets, monitors and reviews environmental objectives, independently of the permit? |  | 1 | 0 |  |  | Available upon request | complete
2.2 | Are there procedures that incorporate environmental issues into the following areas (as supported by demonstrable evidence e.g. written procedures):
|  the control of process change on the installation; |  | 1 | 0 |  |  | Available upon request | complete
|  design and review of new facilities (including provision for their decommisioning), engineering and other capital projects; |  | 1 | 0 |  |  | Available upon request | complete
|  capital approval; |  | 1 | 0 |  |  | Available upon request | complete
|  purchasing policy; |  | 1 | 0 |  |  | Available upon request | complete
2.3 | Are there audits, at least annually, to check that all activities are being carried out in conformity with the above requirements? |  | 1 | 0 |  |  | Available upon request | complete
2.4 | Are they independent? (name the auditing body) |  | 2 | 0 |  |  |  | complete
2.5 | Are there reports annually on environmental performance, objectives and targets, future planned improvements and or facilitate (participate in) local community liaison meetings? |  | 1 | 0 |  |  | Available upon request | complete
All operators need to answer the following two questions
3 | Does your company produce a public environmental statement? You may score in this box for ISO 14001 and industry systems but not for EMAS as this is a requirement for EMAS. | Yes | 1 | 1 |  |  | tata-steel-uk-sustainability-report-2021-2023.pdf | complete | Provide a link to the public environmental statement in cell I83
4 | Within the past 5 years have you failed to meet an improvement condition either set by Natural Resources Wales (NRW) in a Permit or Variation by the due date, without prior agreement? (minus 2 for each failure). ADD NUMBER OF FAILURES NOT Y OR N | None | -2 | 0 |  |  |  | complete
| Organisational Totals |  | 20 | 16 | 80%
2024-04-01
Enforcement History (0 to -40% weighting)
[5 empty] | Enter type of Enforcement | Enter Date enforcement Issued | Enter date that enforcement is, or is due to become completed (spent) in ascending order
1 | Enforcement , Improvement, Works, Compliance or Restoration Notices issued in the past year by Natural Resources Wales (NRW) under any legislation, by the Health and Safety Executive relevant to the COMAH Regulations or by local authorities under Part I of the Environmental Protection Act 1990 or relevant notice or Abatement Notices issued by local authorities or magistrates courts under Part III of the Environmental Protection Act 1990 | 0 | None 0 1st - 5 2nd -10 3rd or more -40
[5 empty] | Enter type of Enforcement | Enter Date enforcement Issued | Date that enforcement is, or is due to become spent
2 | Formal cautions, Enforcement Undertakings or Fixed Monetary Penalties issued by Natural Resources Wales (NRW) in respect of offences under any legislation in the last 3 years. | 0 | None 0 1st - 5 2nd -10 3rd or more -40
[5 empty] | Enter type of Enforcement | Enter Date enforcement Issued | Date that the enforcement is, or is due to become spent
3 | Prohibition, Stop, Suspension or Revocation Notices issued by Natural Resources Wales (NRW) under any legislation, by the Health and Safety Executive relevant to the COMAH Regulations or by local authorities under Part I of the Environmental Protection Act 1990 in the last 3 years | 0 | None 0 1st - 10 2nd or more -40
[5 empty] | Type of conviction | Conviction date | Date that the conviction and/or Penalty (VMP) is, or is due to become spent
4 | Convictions on prosecutions brought by Natural Resources Wales (NRW) under any legislation, by the Health and Safety Executive relevant to the COMAH regulations or by local authorities (in respect of offences under Parts I or III of the Environmental Protection Act 1990) in last 5 years (10 years where imprisonment was imposed). Or any Variable Monetary Penalty (VMP) in the last 5 years. [NB each individual offence counts separately]. | 0 | None 0 1st - 15 2nd or more -40
0
Enforcement History Total
|  | Entered | Spent | Extant | Score
1 | Enforcement etc Notices | 0 | 0 | 0 | 0
2 | Formal Cautions etc | 0 | 0 | 0 | 0
3 | Prohibition etc Notices | 0 | 0 | 0 | 0
4 | Convictions on Prosecutions etc | 0 | 0 | 0 | 0
[5 empty] | 0 | Non capped history
| Enforcement History Total (min -40) |  |  |  | 0 | Capped to -40
Band E= less than 2 D= 2 to 3.99, C= 4 to 5.99, B= 6 to 7.99 , A= 8 to 11 |  |  |  |  | BAND = | A
| Company : | Tata Steel UK Limited |  |  | Permit: | EPR/BL7108IM
Data calculations generating the above graph
| Summary | Max | Score from above | Score as % of Max | Normalised to scale out of 10 | Weighting | Weighted score | Status?
| Operations and Maintenance 20% | 12 | 7 | 58.3333 | 5.8333 | 20 | 1.1667 | Complete
| Training 20% | 17 | 17 | 100 | 10 | 20 | 2 | Complete
| Emergency Planning 20% | 12 | 11 | 91.6667 | 9.1667 | 20 | 1.8333 | Complete | external EMS
| Organisation 40% | 20 | 16 | 80 | 8 | 40 | 3.2 | complete | complete | Incomplete
| Enforcement History Penalty -up to 40% | -40 | 0 | 0 | 0 | 40 | 0
| Overall average weighted score | [5 empty] | 8.2

## 12 EP Summary
Organisation Name: |  | Tata Steel UK Limited
Permit Number: |  | EPR/BL7108IM
|  | Profile before any rules or capping applied |  | Opra Banded Profile used for charging (i.e. after capping and applying rules)
Attribute |  | Number | Band | Number | Band | Status
Complexity |  | 2 | A | 2 | A
|  | 2 | B | 2 | B
|  | 3 | C | 2 | C
|  | 0 | D | 1 | D
|  | 0 | E | 0 | E
Emissions | Air |  | C |  | C
| Water |  | D |  | D
| Land |  | B |  | B
| Sewer |  | - |  | -
| Waste Off Site |  | B |  | B
| Waste Input |  | C |  | C
Location |  |  | E |  | E | Complete
Operator Performance |  |  | A |  | A | Complete

## 13 Calculation
Organisation Name: | Tata Steel UK Limited |  | Permit Number: |  | EPR/BL7108IM
EPR Installations Application Charge Calculation
(excludes Compliance Rating)
Scoring Summary - Financial
Attribute | Band | Number | Score | Total Score
Complexity | A | 2 | 2 | 4
| B | 2 | 15 | 30
| C | 2 | 45 | 90
| D | 1 | 82 | 82
| E | 0 | 110 | 0
Emissions to Air | C |  |  | 20
Emissions to Water | D |  |  | 35
Emissions to Land | B |  |  | 10
Emissions to Sewer | - |  |  | 0
Emissions to Off-site Waste | B |  |  | 2
Emissions - Waste Input | C |  |  | 20
Location | E |  |  | 60 | Complete
Operator Performance | A |  |  | 10 | Complete
| Total Opra charging score |  |  | 363
Part A(2), Part B, MCP and SG Activities
Please ensure that you have completed these entries in the Other Activities sheet. The indicative charge shown here will not include any charges associated with DAA Waste Operation, Part A (2) or Part B or MCP or SG activities that form part of the installation. Refer to Environmental Permitting Charging Scheme for further details.
Link to Environmental Permitting Charges
Indicative Charge |  |  | Opra Charge Multipliers (2025/2026)
Subsistence Charge* | 41745 |  | Subsistence |  |  | 115
* Does not take into account Compliance Rating
OPRA is now only used to calculate annual subsistence charges.
Details of charges, and our new application charge tool can be found on our website

## Picklists
Introduction | Listed activity |  | Other activities | Other activities | [5 empty] | Other activites | Other activities |  |  |  | Locaton |  | Operator performance | [7 empty] | Opra charging mulitpliers
CinC | Schedule 1 | Complexity |  | Schedule activiites | [6 empty] | Rule 4 |  |  |  | Yes |  | Yes |  |  | Yes | No
Yes | 1.1 Part A (1) a) (i) <300MW but >50MW | C | Part A2 or Part B | PartA2 | PartB | PartB_MCP_and_or_SG | DAA_Waste | MCP_and_SG | SG | MCP | Schedule 1 | Complexcity | Aggregation Group |  | No |  | No |  |  | No | N/A
No | 1.1 Part A (1) a) (i) >300MW | D |  | 1.2 Part A(2) (a) | 1.1 Part B a) | 1.1 Part B MCP-Schedule 25A | Waste activity that is not a Part A(1) activity | Schedule 25 A & B - Both an MCP & a Specified Generator | Schedule 25B – Specified generator only | Schedule 25A - Medium combustion plant only | Now linkeddirectly to the main schedule activies |  | 1 | [5 empty] | None | Yes
| 1.2 Part A(1) a) | D |  | 2.1 Part A(2) (a) | 1.1 Part B b) | 1.1 Part B SG-Schedule 25B | [6 empty] | 2 |  |  |  | Yes |  | 1 | [5 empty] | Permit application | 211
| 1.2 Part A(1) b) >250 TPA | E |  | 2.1 Part A(2) (b) | 1.1 Part B c) ii) | 1.1 Part B MCP & SG _Schedule 25 A&B | [6 empty] | 3 |  |  |  | No |  | 2 | [5 empty] | Susbsistance charge | 102
| 1.2 Part A(1) b) <250 TPA | B |  | 2.1 Part A(2) (c) | 1.1 Part B c) i) | 5.1 Part B MCP-Schedule 25A | [6 empty] | 4 |  |  |  | N/A |  | 3 | [5 empty] | Normal vcariaiton | 58
| 1.2 Part A (1) c) (A) | E |  | 2.1 Part A(2) (d) | 1.2 Part B a) | 5.1 Part B SG-Schedule 25B | [6 empty] | 5 | [5 empty] | 4 | [5 empty] | Substantial variaiton | 116
| 1.2 Part A (1) d) | C |  | 2.2 Part A(2) a) | 1.2 Part B b) | 5.1 Part B MCP & SG-Schedule 25A&B | [6 empty] | 6 | [5 empty] | 5 | [5 empty] | Full surrender | 130
| 1.2 Part A(1) e) i) | C |  | 2.3 Part A(2) a) | 1.2 Part B c) | [13 empty] | 5 or more | [5 empty] | Partialo surrnder | 100
| 1.2 Part A(1) e) ii) | C |  | 3.1 Part A(2) a) | 1.2 Part B d)
| 1.2 Part A(1) e) i) or ii) but <500000 TPA | B |  | 3.1 Part A(2) b) | 2.1 Part B a) | [8 empty] | Enforcement , Improvement, Works, Compliance or Restoration Notices issued in the past year by Natural Resources Wales (NRW) under any legislation, by the Health and Safety Executive relevant to the COMAH Regulations or by local authorities under Part I of the Environmental Protection Act 1990 or relevant notice or Abatement Notices issued by local authorities or magistrates courts under Part III of the Environmental Protection Act 1990 | Notice | Formal Caution |  | Prohibition Notice | Prosecution | Enforcement Notice | Improvement notice | Works Notice | Complaince Notice | Restoration Notice
| 1.2 Part A (1) f) | E |  | 3.3 Part A(2) a) | 2.1 Part B b) i) | [9 empty] | Enforcement Notice | Enforcement undertaking |  | Stop Notice | Variable Money Penalty | Formal cautions, Enforcement Undertakings or Fixed Monetary Penalties
| 1.2 Part A (1) f) A) | C |  | 3.5 Part A(2) a) | 2.1 Part B b) ii) | [9 empty] | Improvement notice | Fixed Monetary Penalty |  | Suspension Notice |  | Prohibition, Stop, Suspension or Revocation Notices
| 1.2 Part A (1) g) | E |  | 3.6 Part A (2) a) i) | 2.1 Part B c) | [9 empty] | Works Notice |  |  | Revocation Notice
| 2.1 Part A (1) a) | C |  | 3.6 Part A (2) a) ii) | 2.1 Part B d) i) | [9 empty] | Compliance Notice
| 2.1 Part A (1) b) i or ii | E |  | 5.1 Part A (2) a) | 2.1 Part B d) ii) | [9 empty] | Restoration Notice
| 2.1 Part A (1) b) A | D |  | 5.1 Part A (2) b) | 2.1 Part B d) iii)
| 2.1 Part A (1) c) | C |  | 5.1 Part A (2) c) | 2.1 Part B e)
| 2.1 Part A (1) d) | A |  | 6.1 Part A (2) a) | 2.2 Part B a)
| 2.2 Part A(1) a) | C |  | 6.4 Part A (2) a) | 2.2 Part B b)
| 2.2 Part A(1) b) i) | B |  | 6.7 Part A (2) a) | 2.2 Part B c)
| 2.2 Part A(1) b) ii) | B |  | 6.8 Part A (2) a) | 2.2 Part B d)
| 2.2 Part A(1) c) | A |  |  | 2.2 Part B e)
| 2.3 Part A (1) a) | A |  |  | 2.3 Part B a)
| 3.1 Part A(1) a) | C |  |  | 3.1 Part B a)
| 3.1 Part A(1) b) | C |  |  | 3.1 Part B b)
| 3.2 Part A(1) a) | A |  |  | 3.1 Part B c)
| 3.2 Part A(1) b) | A |  |  | 3.1 Part B d)
| 3.3 Part A(1) a) | A |  |  | 3.3 Part B a)
| 3.4 Part A(1) a) | A |  |  | 3.3 Part B b)
| 3.6 Part A(1) a) | A |  |  | 3.3 Part B c)
| 4.1 Part A1 a) (i) <2000TPA | B |  |  | 3.3 Part B d) i)
| 4.1 Part A1 a) (i) >2000TPA | C |  |  | 3.3 Part B d) ii)
| 4.1 Part A1 a) (ii) <2000TPA | B |  |  | 3.3 Part B e)
| 4.1 Part A1 a) (ii) >2000TPA | C |  |  | 3.5 Part B a)
| 4.1 Part A1 a) (iii) <2000TPA | B |  |  | 3.5 Part B b) i)
| 4.1 Part A1 a) (iii) >2000TPA | C |  |  | 3.5 Part B b) ii)
| 4.1 Part A1 a) (iv) <2000TPA | B |  |  | 3.5 Part B b) iii)
| 4.1 Part A1 a) (iv) >2000TPA | C |  |  | 3.5 Part B c)
| 4.1 Part A1 a) (v) <2000TPA | B |  |  | 3.5 Part B d)
| 4.1 Part A1 a) (v) >2000TPA | C |  |  | 3.5 Part B e)
| 4.1 Part A1 a) (vi) <2000TPA | B |  |  | 3.5 Part B f)
| 4.1 Part A1 a) (vi) >2000TPA | C |  |  | 3.5 Part B g)
| 4.1 Part A1 a) (vii) <2000TPA | B |  |  | 3.6 Part B a)
| 4.1 Part A1 a) (vii) >2000TPA | C |  |  | 3.6 Part B b)
| 4.1 Part A1 a) (viii) <2000TPA | B |  |  | 4.1 Part B a)
| 4.1 Part A1 a) (viii) >2000TPA | C |  |  | 4.1 Part B b)
| 4.1 Part A1 a) (ix) <2000TPA | B |  |  | 4.1 Part B c)
| 4.1 Part A1 a) (ix) >2000TPA | C |  |  | 4.1 Part B d)
| 4.1 Part A1 a) (x) <2000TPA | B |  |  | 4.8 Part B a)
| 4.1 Part A1 a) (x) >2000TPA | C |  |  | 5.1 Part B a)
| 4.1 Part A1 a) (xi) <2000TPA | B |  |  | 5.1 Part B b)
| 4.1 Part A1 a) (xi) >2000TPA | C |  |  | 6.3 Part B a) i)
| 4.1 Part A1 a) (xi) Soap via neutralisation | B |  |  | 6.3 Part B a) ii)
| 4.1 Part A1 a) (A) | A |  |  | 6.4 Part B a) i)
| 4.1 Part A1 a) (B) | A |  |  | 6.4 Part B a) ii)
| 4.1 Part A1 a) (C) | A |  |  | 6.4 Part B a) iii)
| 4.2 Part A1 (a) i) | C |  |  | 6.4 Part B a) iv)
| 4.2 Part A1 (a) ii) | C |  |  | 6.4 Part B b)
| 4.2 Part A1 (a) iii) | C |  |  | 6.4 Part B c) i)
| 4.2 Part A1 (a) iv) | C |  |  | 6.4 Part B c) ii)
| 4.2 Part A1 (a) v) | C |  |  | 6.4 Part B c) iii)
| 4.2 Part A1 (a) vi) | C |  |  | 6.5 Part B a) i)
| 4.2 Part A1 (a) A) | A |  |  | 6.5 Part B a) ii)
| 4.2 Part A1 (a) B) | C |  |  | 6.6 Part B a) i)
| 4.2 Part A1 (b) | A |  |  | 6.6 Part B a) ii)
| 4.2 Part A1 (c) | A |  |  | 6.7 Part B a) i)
| 4.2 Part A1 (d) | A |  |  | 6.7 Part B a) ii)
| 4.2 Part A1 (e) | A |  |  | 6.7 Part B b)
| 4.2 Part A1 (f) | A |  |  | 6.8 Part B a)
| 4.3 Part A1 (a) >100t/TPA | C |  |  | 6.8 Part B b)
| 4.3 Part A1 (a) A)<100TPA | A |  |  | 7 Part B
| 4.3 Part A1 (a) B) | A |  |  | Associated process
| 4.4 Part A1 (a) >2000 TPA | C
| 4.4 Part A1 (a) <2000 TPA | D
| 4.5 Part A1 (a) >2000 TPA | C
| 4.5 Part A1 (a) <2000 TPA | D
| 4.6 Part A1 (a) >2000 TPA | C
| 4.6 Part A1 (a) <2000 TPA | D
| 4.7 Part A1 (a) | A
| 5.1 Part A1 (a) >10 TPD | E
| 5.1 Part A1 (a) (A) | C
| 5.1 Part A1 (a) (B) | C
| 5.1 Part A1 (a) (C) | B
| 5.1 Part A1 (b) | E
| 5.1 Part A1 (b) (A) | C
| 5.1 Part A1 (b) (B) | C
| 5.1 Part A1 (b) (C) | C
| 5.1 Part A1 (b) (D) | B
| 5.1 Part A1 (c) | C
| 5.2 Part A1 (a) Non hazardous | C
| 5.2 Part A1 (a) Hazardous | D
| 5.3 Part A (1) a) (i) | B
| 5.3 Part A (1) a) (ii) | B
| 5.3 Part A (1) a) (ii) (A) | C
| 5.3 Part A (1) a) (ii) (B) | B
| 5.3 Part A (1) a) (ii) (C) | A
| 5.3 Part A (1) a) (iii) | B
| 5.3 Part A (1) a)(iii) (A) | A
| 5.3 Part A (1) a) (iv) | B
| 5.3 Part A (1) a) (iv) (A) | A
| 5.3 Part A (1) a) (v) | A
| 5.3 Part A (1) a) (vi) | A
| 5.3 Part A (1) a) (vii) | A
| 5.3 Part A (1) a) (viii) | A
| 5.3 Part A (1) a) (ix) | A
| 5.3 Part A (1) a) (x) | A
| 5.3 Part A (1) a) (xi) | C
| 5.4 Part A (1) a) (i) | A
| 5.4 Part A (1) a) (ii) | A
| 5.4 Part A (1) a) (iii) | A
| 5.4 Part A (1) a) (iv) | A
| 5.4 Part A (1) a) (v) | A
| 5.4 Part A (1) b) (i) | A
| 5.4 Part A (1) b) (ii) | A
| 5.4 Part A (1) b) (iii) | A
| 5.4 Part A (1) b) (iv) | A
| 5.5 Part A (1) a) | B
| 5.6 Part A (1) a) | B
| 5.6 Part A (1) b) | D
| 5.7 Part A (1) a) | A
| 6.1 Part A (1) a) >50000 TPA | B
| 6.1 Part A (1) a) <50000 TPA | A
| 6.1 Part A (1) b) >50000 TPA | C
| 6.1 Part A (1) b) <50000 TPA | A
| 6.2 Part A (1) a) | A
| 6.3 Part A (1) a) (i) | A
| 6.3 Part A (1) a) (ii) | A
| 6.4 Part A (1) a) | A
| 6.8 Part A (1) a) | B
| 6.8 Part A (1) b) | B
| 6.8 Part A (1) c) | C
| 6.8 Part A (1) c) (A) | A
| 6.8 Part A (1) d) i) | B
| 6.8 Part A (1) d) ii) | B
| 6.8 Part A (1) d) iii) | B
| 6.8 Part A (1) e) | B
| 6.10 Part A (1) a) | E