## Application info
Applicant Information
Instructions: |  |  |  |  | Sample numbers and locations
1. All applicants and laboratories should refer to the most recent guidance on sediment analysis in support of marine licence applications on
| the Marine Licensing pages of the NRW website |  |  |  |  | Sample ID | Excluded sample (NRW PS use) | Sample location (decimal degrees, WGS84) |  | Location name (as per sampling plan) | Sampling depth (m) | Dredge area
2. Full information must be provided under each relevant sheet of the workbook. Grey highlighted cells indicate where information can be entered. | [7 empty] | Position latitude | Position longitude
3. Where information cannot be provided, the applicant should consult with NRW PS prior to submission. | [5 empty] | A |  | 51'23.75N | 003'15.741W | Basin Site A | 10.1 | Area i
4. Worksheets are protected to prevent accidental amendments to calculated values. If amendments are required please consult with NRW PS. | [5 empty] | B |  | 51'23.73N | 003'15.664W | Basin Site B | 7 | Area i
5. Sample IDs used through the data output worksheets should correspond to Sample IDs provided on this worksheet. | [5 empty] | C |  | 51'23.67N | 003'15.742W | Lock Site C | 6.4 | Area i
[6 empty] | D |  | 51'23.54N | 003'15.522W | Harbour Site D | 5.1 | Area ii
[6 empty] | E |  | 51'23.54N | 003'15.522W | Harbour Site E | 9.1 | Area ii
Marine licence applicant information: | [5 empty] | F |  | 51'23.60N | 003'15.530W | Harbour Site F | 3.9 | Area ii
| Applicant: |  | Associated British Ports
| NRW Sample plan reference number: |  | SP2504
| Application title: |  | DML1955v2 - Marine Application - Barry
| Date sampled: |  | 2025-05-07
| Sampling location: |  | Barry
Dredge area tonnages:
| Dredge Area | Dredging tonnages | % total dredged material | Total dredged material
| Area i | 54999 | 55% | 99999
| Area ii | 45000 | 45%
Area iii
Area iv
Area v
Area vi
Do not delete
y

## Physical Data
Physical characteristics data
| Instructions: |  |  | Physical characteristics analysis outputs:
1. Record the laboratory/contractor responsible for analysis
| 2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Visual appearance* | Exempt from chemical analysis▫ | Total Solids (% total sediments) | Organic matter (total organic carbon) | Particle size distribution (% at 0.5 phi intervals)
| 3. Enter full dataset for each sample in the analysis results table | [9 empty] | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
| 4. Where copying and pasting entries please use paste values only | [9 empty] | 45mm | 31.5mm | 22.4mm | 16mm | 11.2mm | 8mm | 5.6mm | 4mm | 2.8mm | 2mm | 1.4mm | 1mm | 707µm | 500µm | 353.6µm | 250µm | 176.8µm | 125µm | 88.39µm | 63µm | 44.2µm | 31.3µm | 22.1µm | 15.6µm | 11µm | 7.8µm | 5.5µm | 3.9µm | 2.75µm | 1.95µm | 1.38µm | 0.98µm | 0.69µm | 0.49µm | 0.34µm | 0.24µm | 0.17µm | 0.12µm | 0.09µm | 0.06µm | 0.04µm | <0.04µm
| 5. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02669.001 | Area i | A | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 39.3 | 2.45 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015667 | 0.53193 | 2.66 | 3.3354 | 4.6602 | 5.695 | 9.0878 | 11.5829 | 12.2454 | 12.0849 | 10.2674 | 7.5734 | 4.9387 | 3.1981 | 2.2751 | 1.9319 | 1.8858 | 1.8452 | 1.6143 | 1.1728 | 0.78898 | 0.44325 | 0.16155 | 0.018469 | 0
|  | IDs should be separated by a comma |  | MAR02669.002 | Area i | B | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 51.5 | 2.43 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.65967 | 5.8721 | 6.1565 | 9.6094 | 12.0029 | 12.2198 | 12.0954 | 10.5833 | 8.1272 | 5.5008 | 3.6443 | 2.6086 | 2.1929 | 2.1004 | 2.0222 | 1.7566 | 1.2825 | 0.86702 | 0.4917 | 0.18487 | 0.022 | 0
|  |  |  | MAR02669.003 | Area i | C | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 39 | 2.39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.26347 | 3.3289 | 4.9364 | 6.1256 | 9.4534 | 12.0104 | 12.7878 | 12.5942 | 10.6423 | 7.7778 | 4.9678 | 3.1311 | 2.2091 | 1.8871 | 1.8338 | 1.7795 | 1.5683 | 1.1784 | 0.82765 | 0.4874 | 0.1875 | 0.022242 | 0
|  |  |  | MAR02669.004 | Area ii | D | Brown Mud with an Anoxic Odour. |  | 45.2 | 2.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0081333 | 1.1583 | 3.616 | 3.5405 | 4.3367 | 5.2401 | 5.9802 | 8.8126 | 10.4845 | 10.8333 | 10.746 | 9.2345 | 6.8788 | 4.5312 | 2.9822 | 2.1588 | 1.8348 | 1.7687 | 1.7182 | 1.5207 | 1.1429 | 0.80338 | 0.47166 | 0.1776 | 0.020443 | 0
| Analysis information: |  |  | MAR02669.005 | Area ii | E | Brown Mud with an Anoxic Odour. |  | 48.6 | 2.28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010967 | 0.6644 | 1.7067 | 2.703 | 4.1964 | 5.5878 | 6.9561 | 10.3852 | 12.9839 | 12.9227 | 11.6243 | 9.0363 | 6.1755 | 3.7406 | 2.283 | 1.6191 | 1.4024 | 1.3508 | 1.2932 | 1.1535 | 0.9094 | 0.6798 | 0.42426 | 0.17011 | 0.020349 | 0
|  |  |  | MAR02669.006 | Area ii | F | Brown Mud with an Anoxic Odour. |  | 42.9 | 2.28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.20963 | 4.4575 | 5.9246 | 6.7029 | 9.9608 | 12.0857 | 12.5532 | 12.1359 | 10.1318 | 7.3603 | 4.6801 | 2.9324 | 2.0542 | 1.7249 | 1.6322 | 1.5529 | 1.3722 | 1.0623 | 0.77609 | 0.47594 | 0.19118 | 0.023307 | 0
|  | Laboratory/contractor: | Ocean Ecology Ltd
|  | Date of analysis: | 2025-05-30
* Visual appearance: Incude a description of what the material looks like and what it contains, e.g. sandy material containing brick fragments, or black silt, or foreign man made matter caught in the sample.
▫ Exempt from chemical analysis: enter 'y' where sediment samples contain glacial material or are too coarse and thus exempt from chemical analysis.
y

## Physical Stats (hidden)
Physical characteristics summary
Physical characteristics statistics:
Analysis information: |  |  |  | Laboratory sample number | Dredge Area | Sample ID | Excluded (y if yes) | Visual appearance | Exempt from chemical analysis | Dry matter (% total sediments) | Organic matter (total organic carbon) |  | Particle size distribution (% at 0.5 phi intervals) | [40 empty] | Particle size summary statistics
[12 empty] | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5 | Gravel (%) | Sand (%) | Very coarse and coarse sand (%) | Medium sand (%) | Fine sand and very fine sand (%) | Silt/Clay (%)
| Applicant: | Associated British Ports | [9 empty] | 45mm | 31.5mm | 22.4mm | 16mm | 11.2mm | 8mm | 5.6mm | 4mm | 2.8mm | 2mm | 1.4mm | 1mm | 707µm | 500µm | 353.6µm | 250µm | 176.8µm | 125µm | 88.39µm | 63µm | 44.2µm | 31.3µm | 22.1µm | 15.6µm | 11µm | 7.8µm | 5.5µm | 3.9µm | 2.75µm | 1.95µm | 1.38µm | 0.98µm | 0.69µm | 0.49µm | 0.34µm | 0.24µm | 0.17µm | 0.12µm | 0.09µm | 0.06µm | 0.04µm | <0.04µm
| Application number: | SP2504 |  | MAR02669.001 | Area i | A |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 39.3 | 2.45 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015667 | 0.53193 | 2.66 | 3.3354 | 4.6602 | 5.695 | 9.0878 | 11.5829 | 12.2454 | 12.0849 | 10.2674 | 7.5734 | 4.9387 | 3.1981 | 2.2751 | 1.9319 | 1.8858 | 1.8452 | 1.6143 | 1.1728 | 0.78898 | 0.44325 | 0.16155 | 0.018469 | 0 | 0 | 3.1935 | 0 | 0 | 3.1935 | 96.8065
| Application title: | DML1955v2 - Marine Application - Barry |  | MAR02669.002 | Area i | B |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 51.5 | 2.43 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.65967 | 5.8721 | 6.1565 | 9.6094 | 12.0029 | 12.2198 | 12.0954 | 10.5833 | 8.1272 | 5.5008 | 3.6443 | 2.6086 | 2.1929 | 2.1004 | 2.0222 | 1.7566 | 1.2825 | 0.86702 | 0.4917 | 0.18487 | 0.022 | 0 | 0 | 0 | 0 | 0 | 0 | 100
| Date sampled: | 2025-05-07 |  | MAR02669.003 | Area i | C |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 39 | 2.39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.26347 | 3.3289 | 4.9364 | 6.1256 | 9.4534 | 12.0104 | 12.7878 | 12.5942 | 10.6423 | 7.7778 | 4.9678 | 3.1311 | 2.2091 | 1.8871 | 1.8338 | 1.7795 | 1.5683 | 1.1784 | 0.82765 | 0.4874 | 0.1875 | 0.022242 | 0 | 0 | 0.26347 | 0 | 0 | 0.26347 | 99.7365
| Sampling location: | Barry |  | MAR02669.004 | Area ii | D |  | Brown Mud with an Anoxic Odour. |  | 45.2 | 2.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0081333 | 1.1583 | 3.616 | 3.5405 | 4.3367 | 5.2401 | 5.9802 | 8.8126 | 10.4845 | 10.8333 | 10.746 | 9.2345 | 6.8788 | 4.5312 | 2.9822 | 2.1588 | 1.8348 | 1.7687 | 1.7182 | 1.5207 | 1.1429 | 0.80338 | 0.47166 | 0.1776 | 0.020443 | 0 | 0 | 8.3229 | 0 | 0 | 8.3229 | 91.6771
|  |  |  | MAR02669.005 | Area ii | E |  | Brown Mud with an Anoxic Odour. |  | 48.6 | 2.28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010967 | 0.6644 | 1.7067 | 2.703 | 4.1964 | 5.5878 | 6.9561 | 10.3852 | 12.9839 | 12.9227 | 11.6243 | 9.0363 | 6.1755 | 3.7406 | 2.283 | 1.6191 | 1.4024 | 1.3508 | 1.2932 | 1.1535 | 0.9094 | 0.6798 | 0.42426 | 0.17011 | 0.020349 | 0 | 0 | 5.0851 | 0 | 0 | 5.0851 | 94.9149
| Laboratory/contractor: | Ocean Ecology Ltd |  | MAR02669.006 | Area ii | F |  | Brown Mud with an Anoxic Odour. |  | 42.9 | 2.28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.20963 | 4.4575 | 5.9246 | 6.7029 | 9.9608 | 12.0857 | 12.5532 | 12.1359 | 10.1318 | 7.3603 | 4.6801 | 2.9324 | 2.0542 | 1.7249 | 1.6322 | 1.5529 | 1.3722 | 1.0623 | 0.77609 | 0.47594 | 0.19118 | 0.023307 | 0 | 0 | 0.20963 | 0 | 0 | 0.20963 | 99.7904
| Date of analysis: | 2025-05-30
|  |  |  | Averages: | [5 empty] | 44.4167 | 2.355 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0031833 | 0.30404 | 0.97577 | 1.5628 | 3.3858 | 5.3702 | 6.2694 | 9.5515 | 11.8584 | 12.2604 | 11.8801 | 9.9826 | 7.3155 | 4.7265 | 3.0285 | 2.1542 | 1.829 | 1.7619 | 1.7019 | 1.4976 | 1.1247 | 0.79049 | 0.4657 | 0.1788 | 0.021135 | 0 | 0 | 2.8458 | 0 | 0 | 2.8458 | 97.1542
Removal of excluded areas
|  |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Excluded (y if yes) | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
|  |  |  | MAR02669.001 | Area i | A |  | 39.3 |  | 0 | 3.1935 | 96.8065
|  |  |  | MAR02669.002 | Area i | B |  | 51.5 |  | 0 | 0 | 100
|  |  |  | MAR02669.003 | Area i | C |  | 39 |  | 0 | 0.26347 | 99.7365
|  |  |  | MAR02669.004 | Area ii | D |  | 45.2 |  | 0 | 8.3229 | 91.6771
|  |  |  | MAR02669.005 | Area ii | E |  | 48.6 |  | 0 | 5.0851 | 94.9149
|  |  |  | MAR02669.006 | Area ii | F |  | 42.9 |  | 0 | 0.20963 | 99.7904
|  |  |  | Averages: |  |  |  | 44.4167 |  | 0 | 2.8458 | 97.1542
Average of dredge areas
[7 empty] | Dredge area | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[7 empty] | Area i | 43.2667 |  | 0 | 1.1523 | 98.8477
[7 empty] | Area ii | 45.5667 |  | 0 | 4.5392 | 95.4608
Area iii
Area iv
Area v
Area vi
PR weightings (dredge area averages multiplied by proportion of total tonnages)
[7 empty] | Dredge area | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[7 empty] | Area i | 23.7965 |  | 0 | 0.63377 | 54.3658
[7 empty] | Area ii | 20.5052 |  | 0 | 2.0427 | 42.9578
Area iii
Area iv
Area v
Area vi
PR average
Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[8 empty] | 44.3017 |  | 0 | 2.6764 | 97.3236

## PSA charts (hidden)
| LSN | 45000 | 31500 | 22400 | 16000 | 11200 | 8000 | 5600 | 4000 | 2800 | 2000 | 1400 | 1000 | 707 | 500 | 353.6 | 250 | 176.8 | 125 | 88.39 | 63 | 44.2 | 31.3 | 22.1 | 15.6 | 11 | 7.8 | 5.5 | 3.9 | 2.75 | 1.95 | 1.38 | 0.98 | 0.69 | 0.49 | 0.34 | 0.24 | 0.17 | 0.12 | 0.09 | 0.06 | 0.04 | 0
x-axis (phi) |  | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
[44 empty] | Area |  | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
y-axis | A | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015667 | 0.53193 | 2.66 | 3.3354 | 4.6602 | 5.695 | 9.0878 | 11.5829 | 12.2454 | 12.0849 | 10.2674 | 7.5734 | 4.9387 | 3.1981 | 2.2751 | 1.9319 | 1.8858 | 1.8452 | 1.6143 | 1.1728 | 0.78898 | 0.44325 | 0.16155 | 0.018469 | 0 | Area i | Area i | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00052222 | 0.17731 | 0.97448 | 2.4413 | 5.1562 | 5.9923 | 9.3835 | 11.8654 | 12.4177 | 12.2582 | 10.4976 | 7.8261 | 5.1358 | 3.3245 | 2.3643 | 2.004 | 1.94 | 1.8823 | 1.6464 | 1.2112 | 0.82788 | 0.47412 | 0.17797 | 0.020904 | 0
| B | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.65967 | 5.8721 | 6.1565 | 9.6094 | 12.0029 | 12.2198 | 12.0954 | 10.5833 | 8.1272 | 5.5008 | 3.6443 | 2.6086 | 2.1929 | 2.1004 | 2.0222 | 1.7566 | 1.2825 | 0.86702 | 0.4917 | 0.18487 | 0.022 | 0 | Area i | Area ii | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0063667 | 0.60756 | 1.7742 | 2.151 | 4.3302 | 5.5842 | 6.5464 | 9.7195 | 11.8514 | 12.1031 | 11.5021 | 9.4675 | 6.8049 | 4.3173 | 2.7325 | 1.944 | 1.654 | 1.5839 | 1.5215 | 1.3488 | 1.0382 | 0.75309 | 0.45729 | 0.17963 | 0.021366 | 0
| C | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.26347 | 3.3289 | 4.9364 | 6.1256 | 9.4534 | 12.0104 | 12.7878 | 12.5942 | 10.6423 | 7.7778 | 4.9678 | 3.1311 | 2.2091 | 1.8871 | 1.8338 | 1.7795 | 1.5683 | 1.1784 | 0.82765 | 0.4874 | 0.1875 | 0.022242 | 0 | Area i | Area iii
| D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0081333 | 1.1583 | 3.616 | 3.5405 | 4.3367 | 5.2401 | 5.9802 | 8.8126 | 10.4845 | 10.8333 | 10.746 | 9.2345 | 6.8788 | 4.5312 | 2.9822 | 2.1588 | 1.8348 | 1.7687 | 1.7182 | 1.5207 | 1.1429 | 0.80338 | 0.47166 | 0.1776 | 0.020443 | 0 | Area ii | Area iv
| E | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010967 | 0.6644 | 1.7067 | 2.703 | 4.1964 | 5.5878 | 6.9561 | 10.3852 | 12.9839 | 12.9227 | 11.6243 | 9.0363 | 6.1755 | 3.7406 | 2.283 | 1.6191 | 1.4024 | 1.3508 | 1.2932 | 1.1535 | 0.9094 | 0.6798 | 0.42426 | 0.17011 | 0.020349 | 0 | Area ii | Area v
| F | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.20963 | 4.4575 | 5.9246 | 6.7029 | 9.9608 | 12.0857 | 12.5532 | 12.1359 | 10.1318 | 7.3603 | 4.6801 | 2.9324 | 2.0542 | 1.7249 | 1.6322 | 1.5529 | 1.3722 | 1.0623 | 0.77609 | 0.47594 | 0.19118 | 0.023307 | 0 | Area ii | Area vi

## Exempt Samples (hidden)
Exempt samples calculations
Exempt samples complete summary
Analysis information: |  |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Excluded (y if yes) | Visual appearance | Exempt from chemical analysis | Conversion to biniomial (hidden column)
| Applicant: | Associated British Ports
| Application number: | SP2504 |  | MAR02669.001 | Area i | A |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 0
| Application title: | DML1955v2 - Marine Application - Barry |  | MAR02669.002 | Area i | B |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 0
| Date sampled: | 2025-05-07 |  | MAR02669.003 | Area i | C |  | Brown Mud with Shell Fragments and an Anoxic Odour. |  | 0
| Sampling location: | Barry |  | MAR02669.004 | Area ii | D |  | Brown Mud with an Anoxic Odour. |  | 0
|  |  |  | MAR02669.005 | Area ii | E |  | Brown Mud with an Anoxic Odour. |  | 0
| Laboratory/contractor: | Ocean Ecology Ltd |  | MAR02669.006 | Area ii | F |  | Brown Mud with an Anoxic Odour. |  | 0
| Date of analysis: | 2025-05-30 | [7 empty] | 0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Total samples and tonnages exempt
|  |  |  | Dredge Area | Total number tested samples | Number exempt samples | Dredge area tonnages | Proportion exempt samples | Tonnage for OSPAR exempt samples reporting
|  |  |  | Area i | 3 | 0 | 54999 | 0 | 0
|  |  |  | Area ii | 3 | 0 | 45000 | 0 | 0
Area iii
Area iv
Area v
Area vi
[5 empty] | Total exempt samples: | 0 |  | Total exempt tonnages: | 0

## Trace metal data
Trace metal data
Instructions: |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for trace metal analysis
2. Record the date the samples were analysed. |  | Laboratory sample number | Dredge Area | Sample ID(s) | Metals as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table |  |  |  |  | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
4. Trace metal analysis results should be reported in mg/kg (ppm) dry weight |  | MAR02669.001 | Area i | A | 11.4 | 0.33 | 39.8 | 43.9 | 0.23 | 31.7 | 62.6 | 230
5. Enter methdological limit of detection for each trace metal prior to inputting raw data |  | MAR02669.002 | Area i | B | 11.9 | 0.31 | 39.1 | 42.3 | 0.25 | 33.3 | 69.6 | 240
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  | MAR02669.003 | Area i | C | 13.9 | 0.25 | 37.1 | 24.7 | 0.19 | 30 | 57.9 | 210
7. Where copying and pasting entries please use paste values only |  | MAR02669.004 | Area ii | D | 13.3 | 0.2 | 35.2 | 21.8 | 0.19 | 29.2 | 54.3 | 187
8. Where entering multiple Sample IDs please use the pop-up form |  | MAR02669.005 | Area ii | E | 15.6 | 0.17 | 40.9 | 23.1 | 0.2 | 34.4 | 63.9 | 202
| IDs should be separated by a comma | MAR02669.006 | Area ii | F | 14.4 | 0.22 | 36 | 22.7 | 0.2 | 32.3 | 61.3 | 190
Analysis information:
Laboratory/contractor:
Date of analysis:
|  | Limits of detection (mg/kg dry weight): |  |  | 0.5 | 0.04 | 0.5 | 0.5 | 0.01 | 0.5 | 0.5 | 2

## Metals and TS Calcs (hidden)
Trace metal summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg dry weight | [7 empty] | Total Solids (%)
| Application number: | SP2504 |  |  |  |  | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
| Application title: | DML1955v2 - Marine Application - Barry | MAR02669.001 | Area i |  | A | 11.4 | 0.33 | 39.8 | 43.9 | 0.23 | 31.7 | 62.6 | 230 | 39.3
| Date sampled: | 2025-05-07 | MAR02669.002 | Area i |  | B | 11.9 | 0.31 | 39.1 | 42.3 | 0.25 | 33.3 | 69.6 | 240 | 51.5
| Sampling location: | Barry | MAR02669.003 | Area i |  | C | 13.9 | 0.25 | 37.1 | 24.7 | 0.19 | 30 | 57.9 | 210 | 39
|  |  | MAR02669.004 | Area ii |  | D | 13.3 | 0.2 | 35.2 | 21.8 | 0.19 | 29.2 | 54.3 | 187 | 45.2
| Laboratory/contractor: |  | MAR02669.005 | Area ii |  | E | 15.6 | 0.17 | 40.9 | 23.1 | 0.2 | 34.4 | 63.9 | 202 | 48.6
| Date of analysis: |  | MAR02669.006 | Area ii |  | F | 14.4 | 0.22 | 36 | 22.7 | 0.2 | 32.3 | 61.3 | 190 | 42.9
[6 empty] | Averages | 13.4167 | 0.24667 | 38.0167 | 29.75 | 0.21 | 31.8167 | 61.6 | 209.8333
[6 empty] | Action level 1: | 20 | 0.4 | 40 | 40 | 0.3 | 20 | 50 | 130
[6 empty] | Action level 2: | 100 | 5 | 400 | 400 | 3 | 200 | 500 | 800
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
|  |  | MAR02669.001 | Area i |  | A | 4.4802 | 0.12969 | 15.6414 | 17.2527 | 0.09039 | 12.4581 | 24.6018 | 90.39 | 39.3
|  |  | MAR02669.002 | Area i |  | B | 6.1285 | 0.15965 | 20.1365 | 21.7845 | 0.12875 | 17.1495 | 35.844 | 123.6 | 51.5
|  |  | MAR02669.003 | Area i |  | C | 5.421 | 0.0975 | 14.469 | 9.633 | 0.0741 | 11.7 | 22.581 | 81.9 | 39
|  |  | MAR02669.004 | Area ii |  | D | 6.0116 | 0.0904 | 15.9104 | 9.8536 | 0.08588 | 13.1984 | 24.5436 | 84.524 | 45.2
|  |  | MAR02669.005 | Area ii |  | E | 7.5816 | 0.08262 | 19.8774 | 11.2266 | 0.0972 | 16.7184 | 31.0554 | 98.172 | 48.6
|  |  | MAR02669.006 | Area ii |  | F | 6.1776 | 0.09438 | 15.444 | 9.7383 | 0.0858 | 13.8567 | 26.2977 | 81.51 | 42.9
[7 empty] | 5.9668 | 0.10904 | 16.9131 | 13.2481 | 0.093687 | 14.1802 | 27.4872 | 93.3493 | 44.4167
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
|  |  | MAR02669.001 | Area i |  | A | 4.4802 | 0.12969 | 15.6414 | 17.2527 | 0.09039 | 12.4581 | 24.6018 | 90.39 | 39.3
|  |  | MAR02669.002 | Area i |  | B | 6.1285 | 0.15965 | 20.1365 | 21.7845 | 0.12875 | 17.1495 | 35.844 | 123.6 | 51.5
|  |  | MAR02669.003 | Area i |  | C | 5.421 | 0.0975 | 14.469 | 9.633 | 0.0741 | 11.7 | 22.581 | 81.9 | 39
|  |  | MAR02669.004 | Area ii |  | D | 6.0116 | 0.0904 | 15.9104 | 9.8536 | 0.08588 | 13.1984 | 24.5436 | 84.524 | 45.2
|  |  | MAR02669.005 | Area ii |  | E | 7.5816 | 0.08262 | 19.8774 | 11.2266 | 0.0972 | 16.7184 | 31.0554 | 98.172 | 48.6
|  |  | MAR02669.006 | Area ii |  | F | 6.1776 | 0.09438 | 15.444 | 9.7383 | 0.0858 | 13.8567 | 26.2977 | 81.51 | 42.9
[7 empty] | 5.9668 | 0.10904 | 16.9131 | 13.2481 | 0.093687 | 14.1802 | 27.4872 | 93.3493 | 44.4167
Average of dredge areas
[6 empty] | Dredge Area | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[6 empty] | Area i | 5.3432 | 0.12895 | 16.749 | 16.2234 | 0.097747 | 13.7692 | 27.6756 | 98.63 | 43.2667
[6 empty] | Area ii | 6.5903 | 0.089133 | 17.0773 | 10.2728 | 0.089627 | 14.5912 | 27.2989 | 88.0687 | 45.5667
Area iii
Area iv
Area v
Area vi
PR weightings (dredge area averages multiplied by proportion of total tonnages)
[6 empty] | Dredge Area | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[6 empty] | Area i | 2.9388 | 0.07092 | 9.2119 | 8.9228 | 0.05376 | 7.573 | 15.2215 | 54.2461 | 23.7965
[6 empty] | Area ii | 2.9656 | 0.04011 | 7.6848 | 4.6228 | 0.040332 | 6.5661 | 12.2846 | 39.6313 | 20.5052
Area iii
Area iv
Area v
Area vi
PR average
[7 empty] | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[7 empty] | 5.9044 | 0.11103 | 16.8967 | 13.5456 | 0.094093 | 14.1391 | 27.5061 | 93.8774 | 44.3017

## Organotins data
Organotin data
Instructions: |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for organotin analysis
2. Record the date the samples were analysed. |  | Laboratory sample number | Dredge Area | Sample ID(s) | Organotins as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table |  |  |  |  | Dibutyltine (DBT) | Tributyltin (TBT)
4. Organotin analysis results should be reported in mg/kg (ppm) dry weight
5. Enter methdological limit of detection for each organotin prior to inputting raw data
6. Where analysis outputs are less than the limits of detection please enter text "<LOD"
7. Where copying and pasting entries please use paste values only
8. Where entering multiple Sample IDs please use the pop-up form
IDs should be separated by a comma
Analysis information:
Laboratory/contractor:
Date of analysis:
Limits of detection (mg/kg dry weight):

## Organotin calcs (hidden)
Organotin summary information
Analysis information: |  |  | Determinand analysis outputs adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg dry weight
| Application number: | SP2504 |  |  |  |  | Dibutyltine (DBT) | Tributyltin (TBT)
| Application title: | DML1955v2 - Marine Application - Barry
| Date sampled: | 2025-05-07
| Sampling location: | Barry
Laboratory/contractor:
Date of analysis:
Averages
[6 empty] | Action level 1: | 0.1 | 0.1
[6 empty] | Action level 2: | 1 | 1
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Average of dredge areas
[6 empty] | Dredge Area | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Area i
Area ii
Area iii
Area iv
Area v
Area vi
Averages:
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Area i
Area ii
Area iii
Area iv
Area v
Area vi
Averages:
PR average
Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)

## PAH data
Polyaromatic hydrocarbon data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for PAH analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | PAHs as dry weight (µg/kg dry weight) | [21 empty] | Total hydrocarbon content (mg/kg)
3. Enter full dataset for each sample in the analysis results table | [5 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
4. Analysis results for individual PAHs should be reported in µg/kg (ppb) dry weight. |  |  | MAR02669.001 | Area i | A | 60.2 | 48 | 111 | 314 | 428 | 544 | 405 | 434 | 402 | 452 | 399 | 350 | 246 | 461 | 92.9 | 597 | 134 | 391 | 226 | 187 | 421 | 480
| THC should be reported as mg/kg (ppm) |  | MAR02669.002 | Area i | B | 55.9 | 42 | 107 | 280 | 389 | 485 | 382 | 379 | 359 | 343 | 338 | 312 | 194 | 409 | 85.8 | 549 | 120 | 390 | 179 | 164 | 375 | 441
5. Enter methdological limit of detection for each PAH prior to inputting raw data |  |  | MAR02669.003 | Area i | C | 259 | 205 | 524 | 1420 | 1790 | 2250 | 1660 | 1750 | 1680 | 1830 | 1890 | 1470 | 988 | 2110 | 391 | 2770 | 577 | 1680 | 938 | 688 | 2000 | 2180
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02669.004 | Area ii | D | 184 | 157 | 360 | 1010 | 1270 | 1540 | 1160 | 1200 | 1180 | 1190 | 1160 | 962 | 698 | 1460 | 280 | 1940 | 399 | 1190 | 651 | 484 | 1330 | 1510
7. Where copying and pasting entries please use paste values only |  |  | MAR02669.005 | Area ii | E | 67 | 33.2 | 87.3 | 219 | 285 | 379 | 294 | 298 | 280 | 327 | 333 | 262 | 177 | 344 | 70.4 | 432 | 102 | 274 | 166 | 116 | 353 | 334
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02669.006 | Area ii | F | 45 | 33.4 | 82.8 | 220 | 280 | 372 | 279 | 287 | 264 | 329 | 327 | 266 | 186 | 335 | 67.5 | 423 | 103 | 281 | 170 | 115 | 340 | 330
IDs should be separated by a comma
Analysis information:
| Laboratory/contractor: | SOCOTEC UK Ltd
| Date of analysis: | 2025-06-12
|  |  | Limits of detection (µg/kg dry weight): |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## PAH calcs (hidden)
Polyaromatic hydrocarbon summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection and transformed to mg/kg
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as mg/kg dry weight | [21 empty] | Total hydrocarbon content (mg/kg)
| Application number: | SP2504 |  |  |  |  | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
| Application title: | DML1955v2 - Marine Application - Barry | MAR02669.001 | Area i |  | A | 0.0602 | 0.048 | 0.111 | 0.314 | 0.428 | 0.544 | 0.405 | 0.434 | 0.402 | 0.452 | 0.399 | 0.35 | 0.246 | 0.461 | 0.0929 | 0.597 | 0.134 | 0.391 | 0.226 | 0.187 | 0.421 | 0.48
| Date sampled: | 2025-05-07 | MAR02669.002 | Area i |  | B | 0.0559 | 0.042 | 0.107 | 0.28 | 0.389 | 0.485 | 0.382 | 0.379 | 0.359 | 0.343 | 0.338 | 0.312 | 0.194 | 0.409 | 0.0858 | 0.549 | 0.12 | 0.39 | 0.179 | 0.164 | 0.375 | 0.441
| Sampling location: | Barry | MAR02669.003 | Area i |  | C | 0.259 | 0.205 | 0.524 | 1.42 | 1.79 | 2.25 | 1.66 | 1.75 | 1.68 | 1.83 | 1.89 | 1.47 | 0.988 | 2.11 | 0.391 | 2.77 | 0.577 | 1.68 | 0.938 | 0.688 | 2 | 2.18
|  |  | MAR02669.004 | Area ii |  | D | 0.184 | 0.157 | 0.36 | 1.01 | 1.27 | 1.54 | 1.16 | 1.2 | 1.18 | 1.19 | 1.16 | 0.962 | 0.698 | 1.46 | 0.28 | 1.94 | 0.399 | 1.19 | 0.651 | 0.484 | 1.33 | 1.51
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02669.005 | Area ii |  | E | 0.067 | 0.0332 | 0.0873 | 0.219 | 0.285 | 0.379 | 0.294 | 0.298 | 0.28 | 0.327 | 0.333 | 0.262 | 0.177 | 0.344 | 0.0704 | 0.432 | 0.102 | 0.274 | 0.166 | 0.116 | 0.353 | 0.334
| Date of analysis: | 2025-06-12 | MAR02669.006 | Area ii |  | F | 0.045 | 0.0334 | 0.0828 | 0.22 | 0.28 | 0.372 | 0.279 | 0.287 | 0.264 | 0.329 | 0.327 | 0.266 | 0.186 | 0.335 | 0.0675 | 0.423 | 0.103 | 0.281 | 0.17 | 0.115 | 0.34 | 0.33
[5 empty] | Averages: |  | 0.11185 | 0.086433 | 0.21202 | 0.57717 | 0.74033 | 0.92833 | 0.69667 | 0.72467 | 0.69417 | 0.74517 | 0.74117 | 0.60367 | 0.41483 | 0.85317 | 0.1646 | 1.1185 | 0.23917 | 0.701 | 0.38833 | 0.29233 | 0.80317 | 0.87917
[6 empty] | Action level 1: | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.01 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 100
Transformation to wet weight and return to µg/kg
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02669.001 | Area i |  | A | 23.6586 | 18.864 | 43.623 | 123.402 | 168.204 | 213.792 | 159.165 | 170.562 | 157.986 | 177.636 | 156.807 | 137.55 | 96.678 | 181.173 | 36.5097 | 234.621 | 52.662 | 153.663 | 88.818 | 73.491 | 165.453 | 188.64
|  |  | MAR02669.002 | Area i |  | B | 28.7885 | 21.63 | 55.105 | 144.2 | 200.335 | 249.775 | 196.73 | 195.185 | 184.885 | 176.645 | 174.07 | 160.68 | 99.91 | 210.635 | 44.187 | 282.735 | 61.8 | 200.85 | 92.185 | 84.46 | 193.125 | 227.115
|  |  | MAR02669.003 | Area i |  | C | 101.01 | 79.95 | 204.36 | 553.8 | 698.1 | 877.5 | 647.4 | 682.5 | 655.2 | 713.7 | 737.1 | 573.3 | 385.32 | 822.9 | 152.49 | 1080.3 | 225.03 | 655.2 | 365.82 | 268.32 | 780 | 850.2
|  |  | MAR02669.004 | Area ii |  | D | 83.168 | 70.964 | 162.72 | 456.52 | 574.04 | 696.08 | 524.32 | 542.4 | 533.36 | 537.88 | 524.32 | 434.824 | 315.496 | 659.92 | 126.56 | 876.88 | 180.348 | 537.88 | 294.252 | 218.768 | 601.16 | 682.52
|  |  | MAR02669.005 | Area ii |  | E | 32.562 | 16.1352 | 42.4278 | 106.434 | 138.51 | 184.194 | 142.884 | 144.828 | 136.08 | 158.922 | 161.838 | 127.332 | 86.022 | 167.184 | 34.2144 | 209.952 | 49.572 | 133.164 | 80.676 | 56.376 | 171.558 | 162.324
|  |  | MAR02669.006 | Area ii |  | F | 19.305 | 14.3286 | 35.5212 | 94.38 | 120.12 | 159.588 | 119.691 | 123.123 | 113.256 | 141.141 | 140.283 | 114.114 | 79.794 | 143.715 | 28.9575 | 181.467 | 44.187 | 120.549 | 72.93 | 49.335 | 145.86 | 141.57
[5 empty] | Averages: |  | 48.082 | 36.9786 | 90.6262 | 246.456 | 316.5515 | 396.8215 | 298.365 | 309.7663 | 296.7945 | 317.654 | 315.7363 | 257.9667 | 177.2033 | 364.2545 | 70.4864 | 477.6592 | 102.2665 | 300.2177 | 165.7802 | 125.125 | 342.8593 | 375.3948
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02669.001 | Area i |  | A | 23.6586 | 18.864 | 43.623 | 123.402 | 168.204 | 213.792 | 159.165 | 170.562 | 157.986 | 177.636 | 156.807 | 137.55 | 96.678 | 181.173 | 36.5097 | 234.621 | 52.662 | 153.663 | 88.818 | 73.491 | 165.453 | 188.64
|  |  | MAR02669.002 | Area i |  | B | 28.7885 | 21.63 | 55.105 | 144.2 | 200.335 | 249.775 | 196.73 | 195.185 | 184.885 | 176.645 | 174.07 | 160.68 | 99.91 | 210.635 | 44.187 | 282.735 | 61.8 | 200.85 | 92.185 | 84.46 | 193.125 | 227.115
|  |  | MAR02669.003 | Area i |  | C | 101.01 | 79.95 | 204.36 | 553.8 | 698.1 | 877.5 | 647.4 | 682.5 | 655.2 | 713.7 | 737.1 | 573.3 | 385.32 | 822.9 | 152.49 | 1080.3 | 225.03 | 655.2 | 365.82 | 268.32 | 780 | 850.2
|  |  | MAR02669.004 | Area ii |  | D | 83.168 | 70.964 | 162.72 | 456.52 | 574.04 | 696.08 | 524.32 | 542.4 | 533.36 | 537.88 | 524.32 | 434.824 | 315.496 | 659.92 | 126.56 | 876.88 | 180.348 | 537.88 | 294.252 | 218.768 | 601.16 | 682.52
|  |  | MAR02669.005 | Area ii |  | E | 32.562 | 16.1352 | 42.4278 | 106.434 | 138.51 | 184.194 | 142.884 | 144.828 | 136.08 | 158.922 | 161.838 | 127.332 | 86.022 | 167.184 | 34.2144 | 209.952 | 49.572 | 133.164 | 80.676 | 56.376 | 171.558 | 162.324
|  |  | MAR02669.006 | Area ii |  | F | 19.305 | 14.3286 | 35.5212 | 94.38 | 120.12 | 159.588 | 119.691 | 123.123 | 113.256 | 141.141 | 140.283 | 114.114 | 79.794 | 143.715 | 28.9575 | 181.467 | 44.187 | 120.549 | 72.93 | 49.335 | 145.86 | 141.57
[5 empty] | Averages: |  | 48.082 | 36.9786 | 90.6262 | 246.456 | 316.5515 | 396.8215 | 298.365 | 309.7663 | 296.7945 | 317.654 | 315.7363 | 257.9667 | 177.2033 | 364.2545 | 70.4864 | 477.6592 | 102.2665 | 300.2177 | 165.7802 | 125.125 | 342.8593 | 375.3948
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02669.001 | Area i |  | A | 23.7 | 18.9 | 43.6 | 123 | 168 | 214 | 159 | 171 | 158 | 178 | 157 | 138 | 96.7 | 181 | 36.5 | 235 | 52.7 | 154 | 88.8 | 73.5 | 165 | 189
|  |  | MAR02669.002 | Area i |  | B | 28.8 | 21.6 | 55.1 | 144 | 200 | 250 | 197 | 195 | 185 | 177 | 174 | 161 | 99.9 | 211 | 44.2 | 283 | 61.8 | 201 | 92.2 | 84.5 | 193 | 227
|  |  | MAR02669.003 | Area i |  | C | 101 | 80 | 204 | 554 | 698 | 878 | 647 | 683 | 655 | 714 | 737 | 573 | 385 | 823 | 152 | 1080 | 225 | 655 | 366 | 268 | 780 | 850
|  |  | MAR02669.004 | Area ii |  | D | 83.2 | 71 | 163 | 457 | 574 | 696 | 524 | 542 | 533 | 538 | 524 | 435 | 315 | 660 | 127 | 877 | 180 | 538 | 294 | 219 | 601 | 683
|  |  | MAR02669.005 | Area ii |  | E | 32.6 | 16.1 | 42.4 | 106 | 139 | 184 | 143 | 145 | 136 | 159 | 162 | 127 | 86 | 167 | 34.2 | 210 | 49.6 | 133 | 80.7 | 56.4 | 172 | 162
|  |  | MAR02669.006 | Area ii |  | F | 19.3 | 14.3 | 35.5 | 94.4 | 120 | 160 | 120 | 123 | 113 | 141 | 140 | 114 | 79.8 | 144 | 29 | 181 | 44.2 | 121 | 72.9 | 49.3 | 146 | 142
[5 empty] | Averages: |  | 48.1 | 36.9833 | 90.6 | 246.4 | 316.5 | 397 | 298.3333 | 309.8333 | 296.6667 | 317.8333 | 315.6667 | 258 | 177.0667 | 364.3333 | 70.4833 | 477.6667 | 102.2167 | 300.3333 | 165.7667 | 125.1167 | 342.8333 | 375.5
Average of dredge areas
[6 empty] | Dredge Area | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[6 empty] | Area i | 51.1667 | 40.1667 | 100.9 | 273.6667 | 355.3333 | 447.3333 | 334.3333 | 349.6667 | 332.6667 | 356.3333 | 356 | 290.6667 | 193.8667 | 405 | 77.5667 | 532.6667 | 113.1667 | 336.6667 | 182.3333 | 142 | 379.3333 | 422 | #DIV/0!
[6 empty] | Area ii | 45.0333 | 33.8 | 80.3 | 219.1333 | 277.6667 | 346.6667 | 262.3333 | 270 | 260.6667 | 279.3333 | 275.3333 | 225.3333 | 160.2667 | 323.6667 | 63.4 | 422.6667 | 91.2667 | 264 | 149.2 | 108.2333 | 306.3333 | 329 | #DIV/0!
Area iii
Area iv
Area v
Area vi
[6 empty] | Averages: | 48.1 | 36.9833 | 90.6 | 246.4 | 316.5 | 397 | 298.3333 | 309.8333 | 296.6667 | 317.8333 | 315.6667 | 258 | 177.0667 | 364.3333 | 70.4833 | 477.6667 | 102.2167 | 300.3333 | 165.7667 | 125.1167 | 342.8333 | 375.5
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[6 empty] | Area i | 28.1414 | 22.0915 | 55.4945 | 150.5154 | 195.4317 | 246.0313 | 183.8818 | 192.3151 | 182.9652 | 195.9817 | 195.7984 | 159.8654 | 106.6258 | 222.7482 | 42.6613 | 292.9643 | 62.2412 | 185.1652 | 100.2825 | 78.0994 | 208.6316 | 232.0981 | #DIV/0!
[6 empty] | Area ii | 20.2652 | 15.2102 | 36.1354 | 98.611 | 124.9512 | 156.0016 | 118.0512 | 121.5012 | 117.3012 | 125.7013 | 123.9012 | 101.401 | 72.1207 | 145.6515 | 28.5303 | 190.2019 | 41.0704 | 118.8012 | 67.1407 | 48.7055 | 137.8514 | 148.0515 | #DIV/0!
Area iii
Area iv
Area v
Area vi
PR average
[7 empty] | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[7 empty] | 48.4066 | 37.3016 | 91.6299 | 249.1264 | 320.383 | 402.0329 | 301.933 | 313.8163 | 300.2663 | 321.683 | 319.6996 | 261.2664 | 178.7465 | 368.3996 | 71.1916 | 483.1662 | 103.3116 | 303.9663 | 167.4232 | 126.8048 | 346.483 | 380.1496

## PCB data
Polychlorinated biphenyl data
Determinand analysis outputs:
Instructions:
1. Record the laboratory/contractor responsible for PCB analysis |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | PCBs as mg/kg dry weight
2. Record the date the samples were analysed. | [5 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
3. Enter full dataset for each sample in the analysis results table | [5 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02669.001 | Area i | A | 0.00219 | 0.00109 | 0.00376 | 0.003 | 0.00072 | 0.00331 | 0.0006 | 0.00281 | 0.00098 | 0.00445 | 0.00031 | 0.00054 | 0.00137 | 0.00253 | 0.00351 | 0.00059 | 0.00157 | 0.00076 | 0.00605 | 0.00437 | 0.00231 | 0.00098 | 0.00217 | 0.00249 | 0.00476
5. Enter methdological limit of detection for each PCB prior to inputting raw data |  |  | MAR02669.002 | Area i | B | 0.00224 | 0.00121 | 0.00388 | 0.00309 | 0.00064 | 0.00343 | 0.0006 | 0.0033 | 0.00075 | 0.00495 | 0.0003 | 0.00055 | 0.00143 | 0.00294 | 0.00362 | 0.00057 | 0.00195 | 0.00073 | 0.00632 | 0.00475 | 0.00259 | 0.00103 | 0.00253 | 0.00273 | 0.00504
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02669.003 | Area i | C | 0.00225 | 0.00102 | 0.00351 | 0.00305 | 0.00071 | 0.003 | 0.00085 | 0.00299 | 0.00082 | 0.0041 | 0.00036 | 0.0005 | 0.00131 | 0.00235 | 0.00329 | 0.00063 | 0.0016 | 0.00063 | 0.00529 | 0.00391 | 0.0022 | 0.00097 | 0.00217 | 0.00248 | 0.00461
7. ICES 7 PCBs are highlighted in bold |  |  | MAR02669.004 | Area ii | D | 0.00174 | 0.00085 | 0.00281 | 0.0022 | 0.00052 | 0.00265 | 0.00052 | 0.0022 | 0.00079 | 0.00359 | 0.00027 | 0.00056 | 0.00103 | 0.0021 | 0.00256 | 0.00049 | 0.00133 | 0.00055 | 0.00456 | 0.00343 | 0.00207 | 0.00078 | 0.00173 | 0.00202 | 0.0038
8. Where copying and pasting entries please use paste values only |  |  | MAR02669.005 | Area ii | E | 0.0021 | 0.00101 | 0.00309 | 0.00266 | 0.00061 | 0.00318 | 0.00051 | 0.00283 | 0.00072 | 0.004 | 0.00034 | 0.00054 | 0.00128 | 0.00221 | 0.00325 | 0.00053 | 0.00149 | 0.00076 | 0.00566 | 0.00399 | 0.0023 | 0.00096 | 0.00202 | 0.00228 | 0.0048
9. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02669.006 | Area ii | F | 0.00229 | 0.00088 | 0.00316 | 0.00286 | 0.00057 | 0.00328 | 0.00054 | 0.00267 | 0.00087 | 0.00402 | 0.0003 | 0.00049 | 0.00136 | 0.00257 | 0.00333 | 0.0006 | 0.00136 | 0.00065 | 0.00548 | 0.00392 | 0.00228 | 0.00095 | 0.00209 | 0.00237 | 0.00437
IDs should be separated by a comma
Analysis information:
| Laboratory/contractor: | SOCOTEC UK Ltd
| Date of analysis: | 2025-06-12
|  |  | Limits of detection (mg/kg dry weight): |  |  | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05

## PCB calcs (hidden)
Polyaromatic hydrocarbon summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg dry weight | [24 empty] | ICES 7 | Total 25 congeners
| Application number: | SP2504 |  |  |  |  | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
| Application title: | DML1955v2 - Marine Application - Barry |  |  |  |  | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
| Date sampled: | 2025-05-07 | MAR02669.001 | Area i |  | A | 0.00219 | 0.00109 | 0.00376 | 0.003 | 0.00072 | 0.00331 | 0.0006 | 0.00281 | 0.00098 | 0.00445 | 0.00031 | 0.00054 | 0.00137 | 0.00253 | 0.00351 | 0.00059 | 0.00157 | 0.00076 | 0.00605 | 0.00437 | 0.00231 | 0.00098 | 0.00217 | 0.00249 | 0.00476 | 0.025 | 0.05722
| Sampling location: | Barry | MAR02669.002 | Area i |  | B | 0.00224 | 0.00121 | 0.00388 | 0.00309 | 0.00064 | 0.00343 | 0.0006 | 0.0033 | 0.00075 | 0.00495 | 0.0003 | 0.00055 | 0.00143 | 0.00294 | 0.00362 | 0.00057 | 0.00195 | 0.00073 | 0.00632 | 0.00475 | 0.00259 | 0.00103 | 0.00253 | 0.00273 | 0.00504 | 0.02638 | 0.06117
|  |  | MAR02669.003 | Area i |  | C | 0.00225 | 0.00102 | 0.00351 | 0.00305 | 0.00071 | 0.003 | 0.00085 | 0.00299 | 0.00082 | 0.0041 | 0.00036 | 0.0005 | 0.00131 | 0.00235 | 0.00329 | 0.00063 | 0.0016 | 0.00063 | 0.00529 | 0.00391 | 0.0022 | 0.00097 | 0.00217 | 0.00248 | 0.00461 | 0.02346 | 0.0546
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02669.004 | Area ii |  | D | 0.00174 | 0.00085 | 0.00281 | 0.0022 | 0.00052 | 0.00265 | 0.00052 | 0.0022 | 0.00079 | 0.00359 | 0.00027 | 0.00056 | 0.00103 | 0.0021 | 0.00256 | 0.00049 | 0.00133 | 0.00055 | 0.00456 | 0.00343 | 0.00207 | 0.00078 | 0.00173 | 0.00202 | 0.0038 | 0.01932 | 0.04515
| Date of analysis: | 2025-06-12 | MAR02669.005 | Area ii |  | E | 0.0021 | 0.00101 | 0.00309 | 0.00266 | 0.00061 | 0.00318 | 0.00051 | 0.00283 | 0.00072 | 0.004 | 0.00034 | 0.00054 | 0.00128 | 0.00221 | 0.00325 | 0.00053 | 0.00149 | 0.00076 | 0.00566 | 0.00399 | 0.0023 | 0.00096 | 0.00202 | 0.00228 | 0.0048 | 0.02313 | 0.05312
|  |  | MAR02669.006 | Area ii |  | F | 0.00229 | 0.00088 | 0.00316 | 0.00286 | 0.00057 | 0.00328 | 0.00054 | 0.00267 | 0.00087 | 0.00402 | 0.0003 | 0.00049 | 0.00136 | 0.00257 | 0.00333 | 0.0006 | 0.00136 | 0.00065 | 0.00548 | 0.00392 | 0.00228 | 0.00095 | 0.00209 | 0.00237 | 0.00437 | 0.02363 | 0.05326
[5 empty] | Averages: |  | 0.002135 | 0.00101 | 0.0033683 | 0.00281 | 0.00062833 | 0.0031417 | 0.00060333 | 0.0028 | 0.00082167 | 0.004185 | 0.00031333 | 0.00053 | 0.0012967 | 0.00245 | 0.00326 | 0.00056833 | 0.00155 | 0.00068 | 0.00556 | 0.0040617 | 0.0022917 | 0.000945 | 0.0021183 | 0.002395 | 0.0045633 | 0.023487 | 0.054087
[6 empty] | Action level 1: | [25 empty] | 0.01 | 0.02
[6 empty] | Action level 2: | [26 empty] | 0.2
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02669.001 | Area i |  | A | 0.00086067 | 0.00042837 | 0.0014777 | 0.001179 | 0.00028296 | 0.0013008 | 0.0002358 | 0.0011043 | 0.00038514 | 0.0017488 | 0.00012183 | 0.00021222 | 0.00053841 | 0.00099429 | 0.0013794 | 0.00023187 | 0.00061701 | 0.00029868 | 0.0023776 | 0.0017174 | 0.00090783 | 0.00038514 | 0.00085281 | 0.00097857 | 0.0018707 | 0.009825 | 0.022487
|  |  | MAR02669.002 | Area i |  | B | 0.0011536 | 0.00062315 | 0.0019982 | 0.0015914 | 0.0003296 | 0.0017664 | 0.000309 | 0.0016995 | 0.00038625 | 0.0025493 | 0.0001545 | 0.00028325 | 0.00073645 | 0.0015141 | 0.0018643 | 0.00029355 | 0.0010042 | 0.00037595 | 0.0032548 | 0.0024463 | 0.0013338 | 0.00053045 | 0.001303 | 0.0014059 | 0.0025956 | 0.013586 | 0.031503
|  |  | MAR02669.003 | Area i |  | C | 0.0008775 | 0.0003978 | 0.0013689 | 0.0011895 | 0.0002769 | 0.00117 | 0.0003315 | 0.0011661 | 0.0003198 | 0.001599 | 0.0001404 | 0.000195 | 0.0005109 | 0.0009165 | 0.0012831 | 0.0002457 | 0.000624 | 0.0002457 | 0.0020631 | 0.0015249 | 0.000858 | 0.0003783 | 0.0008463 | 0.0009672 | 0.0017979 | 0.0091494 | 0.021294
|  |  | MAR02669.004 | Area ii |  | D | 0.00078648 | 0.0003842 | 0.0012701 | 0.0009944 | 0.00023504 | 0.0011978 | 0.00023504 | 0.0009944 | 0.00035708 | 0.0016227 | 0.00012204 | 0.00025312 | 0.00046556 | 0.0009492 | 0.0011571 | 0.00022148 | 0.00060116 | 0.0002486 | 0.0020611 | 0.0015504 | 0.00093564 | 0.00035256 | 0.00078196 | 0.00091304 | 0.0017176 | 0.0087326 | 0.020408
|  |  | MAR02669.005 | Area ii |  | E | 0.0010206 | 0.00049086 | 0.0015017 | 0.0012928 | 0.00029646 | 0.0015455 | 0.00024786 | 0.0013754 | 0.00034992 | 0.001944 | 0.00016524 | 0.00026244 | 0.00062208 | 0.0010741 | 0.0015795 | 0.00025758 | 0.00072414 | 0.00036936 | 0.0027508 | 0.0019391 | 0.0011178 | 0.00046656 | 0.00098172 | 0.0011081 | 0.0023328 | 0.011241 | 0.025816
|  |  | MAR02669.006 | Area ii |  | F | 0.00098241 | 0.00037752 | 0.0013556 | 0.0012269 | 0.00024453 | 0.0014071 | 0.00023166 | 0.0011454 | 0.00037323 | 0.0017246 | 0.0001287 | 0.00021021 | 0.00058344 | 0.0011025 | 0.0014286 | 0.0002574 | 0.00058344 | 0.00027885 | 0.0023509 | 0.0016817 | 0.00097812 | 0.00040755 | 0.00089661 | 0.0010167 | 0.0018747 | 0.010137 | 0.022849
[5 empty] | Averages: |  | 0.00094688 | 0.00045032 | 0.0014954 | 0.0012457 | 0.00027758 | 0.0013979 | 0.00026514 | 0.0012475 | 0.0003619 | 0.0018647 | 0.00013878 | 0.00023604 | 0.00057614 | 0.0010918 | 0.0014487 | 0.00025126 | 0.00069233 | 0.00030286 | 0.0024764 | 0.00181 | 0.0010219 | 0.00042009 | 0.00094372 | 0.0010649 | 0.0020316 | 0.010445 | 0.024059
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02669.001 | Area i |  | A | 0.00086067 | 0.00042837 | 0.0014777 | 0.001179 | 0.00028296 | 0.0013008 | 0.0002358 | 0.0011043 | 0.00038514 | 0.0017488 | 0.00012183 | 0.00021222 | 0.00053841 | 0.00099429 | 0.0013794 | 0.00023187 | 0.00061701 | 0.00029868 | 0.0023776 | 0.0017174 | 0.00090783 | 0.00038514 | 0.00085281 | 0.00097857 | 0.0018707 | 0.009825 | 0.022487
|  |  | MAR02669.002 | Area i |  | B | 0.0011536 | 0.00062315 | 0.0019982 | 0.0015914 | 0.0003296 | 0.0017664 | 0.000309 | 0.0016995 | 0.00038625 | 0.0025493 | 0.0001545 | 0.00028325 | 0.00073645 | 0.0015141 | 0.0018643 | 0.00029355 | 0.0010042 | 0.00037595 | 0.0032548 | 0.0024463 | 0.0013338 | 0.00053045 | 0.001303 | 0.0014059 | 0.0025956 | 0.013586 | 0.031503
|  |  | MAR02669.003 | Area i |  | C | 0.0008775 | 0.0003978 | 0.0013689 | 0.0011895 | 0.0002769 | 0.00117 | 0.0003315 | 0.0011661 | 0.0003198 | 0.001599 | 0.0001404 | 0.000195 | 0.0005109 | 0.0009165 | 0.0012831 | 0.0002457 | 0.000624 | 0.0002457 | 0.0020631 | 0.0015249 | 0.000858 | 0.0003783 | 0.0008463 | 0.0009672 | 0.0017979 | 0.0091494 | 0.021294
|  |  | MAR02669.004 | Area ii |  | D | 0.00078648 | 0.0003842 | 0.0012701 | 0.0009944 | 0.00023504 | 0.0011978 | 0.00023504 | 0.0009944 | 0.00035708 | 0.0016227 | 0.00012204 | 0.00025312 | 0.00046556 | 0.0009492 | 0.0011571 | 0.00022148 | 0.00060116 | 0.0002486 | 0.0020611 | 0.0015504 | 0.00093564 | 0.00035256 | 0.00078196 | 0.00091304 | 0.0017176 | 0.0087326 | 0.020408
|  |  | MAR02669.005 | Area ii |  | E | 0.0010206 | 0.00049086 | 0.0015017 | 0.0012928 | 0.00029646 | 0.0015455 | 0.00024786 | 0.0013754 | 0.00034992 | 0.001944 | 0.00016524 | 0.00026244 | 0.00062208 | 0.0010741 | 0.0015795 | 0.00025758 | 0.00072414 | 0.00036936 | 0.0027508 | 0.0019391 | 0.0011178 | 0.00046656 | 0.00098172 | 0.0011081 | 0.0023328 | 0.011241 | 0.025816
|  |  | MAR02669.006 | Area ii |  | F | 0.00098241 | 0.00037752 | 0.0013556 | 0.0012269 | 0.00024453 | 0.0014071 | 0.00023166 | 0.0011454 | 0.00037323 | 0.0017246 | 0.0001287 | 0.00021021 | 0.00058344 | 0.0011025 | 0.0014286 | 0.0002574 | 0.00058344 | 0.00027885 | 0.0023509 | 0.0016817 | 0.00097812 | 0.00040755 | 0.00089661 | 0.0010167 | 0.0018747 | 0.010137 | 0.022849
[5 empty] | Averages: |  | 0.00094688 | 0.00045032 | 0.0014954 | 0.0012457 | 0.00027758 | 0.0013979 | 0.00026514 | 0.0012475 | 0.0003619 | 0.0018647 | 0.00013878 | 0.00023604 | 0.00057614 | 0.0010918 | 0.0014487 | 0.00025126 | 0.00069233 | 0.00030286 | 0.0024764 | 0.00181 | 0.0010219 | 0.00042009 | 0.00094372 | 0.0010649 | 0.0020316 | 0.010445 | 0.024059
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02669.001 | Area i |  | A | 0.000861 | 0.000428 | 0.00148 | 0.00118 | 0.000283 | 0.0013 | 0.000236 | 0.0011 | 0.000385 | 0.00175 | 0.000122 | 0.000212 | 0.000538 | 0.000994 | 0.00138 | 0.000232 | 0.000617 | 0.000299 | 0.00238 | 0.00172 | 0.000908 | 0.000385 | 0.000853 | 0.000979 | 0.00187 | 0.00983 | 0.0225
|  |  | MAR02669.002 | Area i |  | B | 0.00115 | 0.000623 | 0.002 | 0.00159 | 0.00033 | 0.00177 | 0.000309 | 0.0017 | 0.000386 | 0.00255 | 0.000155 | 0.000283 | 0.000736 | 0.00151 | 0.00186 | 0.000294 | 0.001 | 0.000376 | 0.00325 | 0.00245 | 0.00133 | 0.00053 | 0.0013 | 0.00141 | 0.0026 | 0.0136 | 0.0315
|  |  | MAR02669.003 | Area i |  | C | 0.000878 | 0.000398 | 0.00137 | 0.00119 | 0.000277 | 0.00117 | 0.000332 | 0.00117 | 0.00032 | 0.0016 | 0.00014 | 0.000195 | 0.000511 | 0.000917 | 0.00128 | 0.000246 | 0.000624 | 0.000246 | 0.00206 | 0.00152 | 0.000858 | 0.000378 | 0.000846 | 0.000967 | 0.0018 | 0.00915 | 0.0213
|  |  | MAR02669.004 | Area ii |  | D | 0.000786 | 0.000384 | 0.00127 | 0.000994 | 0.000235 | 0.0012 | 0.000235 | 0.000994 | 0.000357 | 0.00162 | 0.000122 | 0.000253 | 0.000466 | 0.000949 | 0.00116 | 0.000221 | 0.000601 | 0.000249 | 0.00206 | 0.00155 | 0.000936 | 0.000353 | 0.000782 | 0.000913 | 0.00172 | 0.00873 | 0.0204
|  |  | MAR02669.005 | Area ii |  | E | 0.00102 | 0.000491 | 0.0015 | 0.00129 | 0.000296 | 0.00155 | 0.000248 | 0.00138 | 0.00035 | 0.00194 | 0.000165 | 0.000262 | 0.000622 | 0.00107 | 0.00158 | 0.000258 | 0.000724 | 0.000369 | 0.00275 | 0.00194 | 0.00112 | 0.000467 | 0.000982 | 0.00111 | 0.00233 | 0.0112 | 0.0258
|  |  | MAR02669.006 | Area ii |  | F | 0.000982 | 0.000378 | 0.00136 | 0.00123 | 0.000245 | 0.00141 | 0.000232 | 0.00115 | 0.000373 | 0.00172 | 0.000129 | 0.00021 | 0.000583 | 0.0011 | 0.00143 | 0.000257 | 0.000583 | 0.000279 | 0.00235 | 0.00168 | 0.000978 | 0.000408 | 0.000897 | 0.00102 | 0.00187 | 0.0101 | 0.0228
[5 empty] | Averages: |  | 0.00094617 | 0.00045033 | 0.0014967 | 0.0012457 | 0.00027767 | 0.0014 | 0.00026533 | 0.001249 | 0.00036183 | 0.0018633 | 0.00013883 | 0.00023583 | 0.000576 | 0.00109 | 0.0014483 | 0.00025133 | 0.0006915 | 0.000303 | 0.002475 | 0.00181 | 0.0010217 | 0.00042017 | 0.00094333 | 0.0010665 | 0.0020317 | 0.010435 | 0.02405
Average of dredge areas
[6 empty] | Dredge Area | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[6 empty] | Area i | 0.000963 | 0.000483 | 0.0016167 | 0.00132 | 0.00029667 | 0.0014133 | 0.00029233 | 0.0013233 | 0.00036367 | 0.0019667 | 0.000139 | 0.00023 | 0.000595 | 0.0011403 | 0.0015067 | 0.00025733 | 0.000747 | 0.000307 | 0.0025633 | 0.0018967 | 0.001032 | 0.000431 | 0.00099967 | 0.0011187 | 0.00209 | 0.01086 | 0.0251
[6 empty] | Area ii | 0.00092933 | 0.00041767 | 0.0013767 | 0.0011713 | 0.00025867 | 0.0013867 | 0.00023833 | 0.0011747 | 0.00036 | 0.00176 | 0.00013867 | 0.00024167 | 0.000557 | 0.0010397 | 0.00139 | 0.00024533 | 0.000636 | 0.000299 | 0.0023867 | 0.0017233 | 0.0010113 | 0.00040933 | 0.000887 | 0.0010143 | 0.0019733 | 0.01001 | 0.023
Area iii
Area iv
Area v
Area vi
[6 empty] | Averages: | 0.00094617 | 0.00045033 | 0.0014967 | 0.0012457 | 0.00027767 | 0.0014 | 0.00026533 | 0.001249 | 0.00036183 | 0.0018633 | 0.00013883 | 0.00023583 | 0.000576 | 0.00109 | 0.0014483 | 0.00025133 | 0.0006915 | 0.000303 | 0.002475 | 0.00181 | 0.0010217 | 0.00042017 | 0.00094333 | 0.0010665 | 0.0020317 | 0.010435 | 0.02405
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[6 empty] | Area i | 0.00052965 | 0.00026565 | 0.00088916 | 0.00072599 | 0.00016317 | 0.00077733 | 0.00016078 | 0.00072783 | 0.00020002 | 0.0010817 | 7.6449e-05 | 0.0001265 | 0.00032725 | 0.00062718 | 0.00082866 | 0.00014153 | 0.00041085 | 0.00016885 | 0.0014098 | 0.0010432 | 0.0005676 | 0.00023705 | 0.00054981 | 0.00061526 | 0.0011495 | 0.005973 | 0.013805
[6 empty] | Area ii | 0.0004182 | 0.00018795 | 0.00061951 | 0.00052711 | 0.0001164 | 0.00062401 | 0.00010725 | 0.00052861 | 0.000162 | 0.00079201 | 6.2401e-05 | 0.00010875 | 0.00025065 | 0.00046785 | 0.00062551 | 0.0001104 | 0.0002862 | 0.00013455 | 0.001074 | 0.00077551 | 0.0004551 | 0.0001842 | 0.00039915 | 0.00045645 | 0.00088801 | 0.0045045 | 0.01035
Area iii
Area iv
Area v
Area vi
PR average
[7 empty] | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[7 empty] | 0.00094785 | 0.0004536 | 0.0015087 | 0.0012531 | 0.00027957 | 0.0014013 | 0.00026803 | 0.0012564 | 0.00036202 | 0.0018737 | 0.00013885 | 0.00023525 | 0.0005779 | 0.001095 | 0.0014542 | 0.00025193 | 0.00069705 | 0.0003034 | 0.0024838 | 0.0018187 | 0.0010227 | 0.00042125 | 0.00094897 | 0.0010717 | 0.0020375 | 0.010477 | 0.024155

## Organochlorine data
Organochlorine data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Organochlorine pesticides as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table | [5 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02669.001 | Area i | A | <LOD | <LOD | <LOD | 0.0014 | 0.0002 | 0.0004 | <LOD | 0.001
5. Enter methdological limit of detection for each Organochlorine prior to inputting raw data |  |  | MAR02669.002 | Area i | B | <LOD | <LOD | <LOD | 0.0013 | 0.0003 | 0.0004 | <LOD | 0.001
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02669.003 | Area i | C | <LOD | <LOD | <LOD | 0.0005 | 0.0004 | 0.0005 | <LOD | 0.0007
7. Where copying and pasting entries please use paste values only |  |  | MAR02669.004 | Area ii | D | <LOD | <LOD | <LOD | 0.0001 | 0.0003 | 0.0003 | <LOD | 0.0007
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02669.005 | Area ii | E | <LOD | <LOD | <LOD | <LOD | 0.0003 | 0.0001 | 0.0007 | 0.0003
| IDs should be separated by a comma |  | MAR02669.006 | Area ii | F | <LOD | <LOD | <LOD | 0.0001 | 0.0003 | 0.0003 | 0.0001 | 0.0009
Analysis information:
| Laboratory/contractor: | SOCOTEC UK Ltd
| Date of analysis: | 2025-06-12
|  |  | Limits of detection (mg/kg dry weight): |  |  | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001

## Organochlorine calcs (hidden)
Organochlorine summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg dry weight
| Application number: | SP2504 |  |  |  |  | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
| Application title: | DML1955v2 - Marine Application - Barry | MAR02669.001 | Area i |  | A | 0.0001 | 0.0001 | 0.0001 | 0.0014 | 0.0002 | 0.0004 | 0.0001 | 0.001
| Date sampled: | 2025-05-07 | MAR02669.002 | Area i |  | B | 0.0001 | 0.0001 | 0.0001 | 0.0013 | 0.0003 | 0.0004 | 0.0001 | 0.001
| Sampling location: | Barry | MAR02669.003 | Area i |  | C | 0.0001 | 0.0001 | 0.0001 | 0.0005 | 0.0004 | 0.0005 | 0.0001 | 0.0007
|  |  | MAR02669.004 | Area ii |  | D | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0003 | 0.0001 | 0.0007
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02669.005 | Area ii |  | E | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0001 | 0.0007 | 0.0003
| Date of analysis: | 2025-06-12 | MAR02669.006 | Area ii |  | F | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0003 | 0.0001 | 0.0009
[5 empty] | Averages: |  | 0.0001 | 0.0001 | 0.0001 | 0.00058333 | 0.0003 | 0.00033333 | 0.0002 | 0.00076667
[6 empty] | Action level 1: |  |  |  | 0.005 |  |  | 0.001
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02669.001 | Area i |  | A | 3.93e-05 | 3.93e-05 | 3.93e-05 | 0.0005502 | 7.86e-05 | 0.0001572 | 3.93e-05 | 0.000393
|  |  | MAR02669.002 | Area i |  | B | 5.15e-05 | 5.15e-05 | 5.15e-05 | 0.0006695 | 0.0001545 | 0.000206 | 5.15e-05 | 0.000515
|  |  | MAR02669.003 | Area i |  | C | 3.9e-05 | 3.9e-05 | 3.9e-05 | 0.000195 | 0.000156 | 0.000195 | 3.9e-05 | 0.000273
|  |  | MAR02669.004 | Area ii |  | D | 4.52e-05 | 4.52e-05 | 4.52e-05 | 4.52e-05 | 0.0001356 | 0.0001356 | 4.52e-05 | 0.0003164
|  |  | MAR02669.005 | Area ii |  | E | 4.86e-05 | 4.86e-05 | 4.86e-05 | 4.86e-05 | 0.0001458 | 4.86e-05 | 0.0003402 | 0.0001458
|  |  | MAR02669.006 | Area ii |  | F | 4.29e-05 | 4.29e-05 | 4.29e-05 | 4.29e-05 | 0.0001287 | 0.0001287 | 4.29e-05 | 0.0003861
[5 empty] | Averages: |  | 4.4417e-05 | 4.4417e-05 | 4.4417e-05 | 0.00025857 | 0.0001332 | 0.00014518 | 9.3017e-05 | 0.00033822
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02669.001 | Area i |  | A | 3.93e-05 | 3.93e-05 | 3.93e-05 | 0.0005502 | 7.86e-05 | 0.0001572 | 3.93e-05 | 0.000393
|  |  | MAR02669.002 | Area i |  | B | 5.15e-05 | 5.15e-05 | 5.15e-05 | 0.0006695 | 0.0001545 | 0.000206 | 5.15e-05 | 0.000515
|  |  | MAR02669.003 | Area i |  | C | 3.9e-05 | 3.9e-05 | 3.9e-05 | 0.000195 | 0.000156 | 0.000195 | 3.9e-05 | 0.000273
|  |  | MAR02669.004 | Area ii |  | D | 4.52e-05 | 4.52e-05 | 4.52e-05 | 4.52e-05 | 0.0001356 | 0.0001356 | 4.52e-05 | 0.0003164
|  |  | MAR02669.005 | Area ii |  | E | 4.86e-05 | 4.86e-05 | 4.86e-05 | 4.86e-05 | 0.0001458 | 4.86e-05 | 0.0003402 | 0.0001458
|  |  | MAR02669.006 | Area ii |  | F | 4.29e-05 | 4.29e-05 | 4.29e-05 | 4.29e-05 | 0.0001287 | 0.0001287 | 4.29e-05 | 0.0003861
[5 empty] | Averages: |  | 4.4417e-05 | 4.4417e-05 | 4.4417e-05 | 0.00025857 | 0.0001332 | 0.00014518 | 9.3017e-05 | 0.00033822
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02669.001 | Area i |  | A | 3.93e-05 | 3.93e-05 | 3.93e-05 | 0.00055 | 7.86e-05 | 0.000157 | 3.93e-05 | 0.000393
|  |  | MAR02669.002 | Area i |  | B | 5.15e-05 | 5.15e-05 | 5.15e-05 | 0.00067 | 0.000155 | 0.000206 | 5.15e-05 | 0.000515
|  |  | MAR02669.003 | Area i |  | C | 3.9e-05 | 3.9e-05 | 3.9e-05 | 0.000195 | 0.000156 | 0.000195 | 3.9e-05 | 0.000273
|  |  | MAR02669.004 | Area ii |  | D | 4.52e-05 | 4.52e-05 | 4.52e-05 | 4.52e-05 | 0.000136 | 0.000136 | 4.52e-05 | 0.000316
|  |  | MAR02669.005 | Area ii |  | E | 4.86e-05 | 4.86e-05 | 4.86e-05 | 4.86e-05 | 0.000146 | 4.86e-05 | 0.00034 | 0.000146
|  |  | MAR02669.006 | Area ii |  | F | 4.29e-05 | 4.29e-05 | 4.29e-05 | 4.29e-05 | 0.000129 | 0.000129 | 4.29e-05 | 0.000386
[5 empty] | Averages: |  | 4.4417e-05 | 4.4417e-05 | 4.4417e-05 | 0.00025862 | 0.00013343 | 0.00014527 | 9.2983e-05 | 0.00033817
Average of dredge areas
[6 empty] | Dredge Area | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[6 empty] | Area i | 4.3267e-05 | 4.3267e-05 | 4.3267e-05 | 0.00047167 | 0.00012987 | 0.000186 | 4.3267e-05 | 0.00039367
[6 empty] | Area ii | 4.5567e-05 | 4.5567e-05 | 4.5567e-05 | 4.5567e-05 | 0.000137 | 0.00010453 | 0.0001427 | 0.00028267
Area iii
Area iv
Area v
Area vi
[6 empty] | Averages: | 4.4417e-05 | 4.4417e-05 | 4.4417e-05 | 0.00025862 | 0.00013343 | 0.00014527 | 9.2983e-05 | 0.00033817
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[6 empty] | Area i | 2.3796e-05 | 2.3796e-05 | 2.3796e-05 | 0.00025941 | 7.1426e-05 | 0.0001023 | 2.3796e-05 | 0.00021651
[6 empty] | Area ii | 2.0505e-05 | 2.0505e-05 | 2.0505e-05 | 2.0505e-05 | 6.1651e-05 | 4.704e-05 | 6.4216e-05 | 0.0001272
Area iii
Area iv
Area v
Area vi
PR average
Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[7 empty] | 4.4302e-05 | 4.4302e-05 | 4.4302e-05 | 0.00027992 | 0.00013308 | 0.00014934 | 8.8012e-05 | 0.00034372

## BDE data
Brominated flame retardant data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Brominated flame retardants as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table | [5 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02669.001 | Area i | A | 7e-05 | <LOD | 0.0001 | 7e-05 | 7e-05 | 8e-05 | 0.0352 | 5e-05 | 0.00052 | 9e-05 | <LOD | 0.00047
5. Enter methdological limit of detection for each BDE prior to inputting raw data |  |  | MAR02669.002 | Area i | B | 0.00011 | <LOD | 0.00012 | 9e-05 | 8e-05 | 9e-05 | 0.0527 | 7e-05 | 0.00071 | 0.00012 | <LOD | 0.00055
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02669.003 | Area i | C | 7e-05 | <LOD | 7e-05 | 8e-05 | <LOD | 6e-05 | 0.0287 | <LOD | 0.00045 | 7e-05 | <LOD | 0.00031
7. Where copying and pasting entries please use paste values only |  |  | MAR02669.004 | Area ii | D | <LOD | <LOD | 5e-05 | 0.00011 | <LOD | <LOD | 0.0312 | <LOD | 0.00045 | 7e-05 | <LOD | 0.00026
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02669.005 | Area ii | E | 7e-05 | <LOD | 8e-05 | 0.00014 | <LOD | <LOD | 0.0328 | <LOD | 0.00069 | 9e-05 | <LOD | 0.00033
| IDs should be separated by a comma |  | MAR02669.006 | Area ii | F | 8e-05 | <LOD | 0.00012 | 0.00436 | <LOD | 6e-05 | 0.0295 | <LOD | 0.00045 | 8e-05 | <LOD | 0.00029
Analysis information:
| Laboratory/contractor: | SOCOTEC
| Date of analysis: | 2025-06-17
|  |  | Limits of detection (mg/kg dry weight): |  |  | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0005 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05

## BDE calcs (hidden)
Brominated flame retardant summary information
Analysis information: |  |  | determinand analysis outputs - adjusted for limits of detection
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg dry weight
| Application number: | SP2504 |  |  |  |  | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
| Application title: | DML1955v2 - Marine Application - Barry | MAR02669.001 | Area i |  | A | 7e-05 | 5e-05 | 0.0001 | 7e-05 | 7e-05 | 8e-05 | 0.0352 | 5e-05 | 0.00052 | 9e-05 | 5e-05 | 0.00047
| Date sampled: | 2025-05-07 | MAR02669.002 | Area i |  | B | 0.00011 | 5e-05 | 0.00012 | 9e-05 | 8e-05 | 9e-05 | 0.0527 | 7e-05 | 0.00071 | 0.00012 | 5e-05 | 0.00055
| Sampling location: | Barry | MAR02669.003 | Area i |  | C | 7e-05 | 5e-05 | 7e-05 | 8e-05 | 5e-05 | 6e-05 | 0.0287 | 5e-05 | 0.00045 | 7e-05 | 5e-05 | 0.00031
|  |  | MAR02669.004 | Area ii |  | D | 5e-05 | 5e-05 | 5e-05 | 0.00011 | 5e-05 | 5e-05 | 0.0312 | 5e-05 | 0.00045 | 7e-05 | 5e-05 | 0.00026
| Laboratory/contractor: | SOCOTEC | MAR02669.005 | Area ii |  | E | 7e-05 | 5e-05 | 8e-05 | 0.00014 | 5e-05 | 5e-05 | 0.0328 | 5e-05 | 0.00069 | 9e-05 | 5e-05 | 0.00033
| Date of analysis: | 2025-06-17 | MAR02669.006 | Area ii |  | F | 8e-05 | 5e-05 | 0.00012 | 0.00436 | 5e-05 | 6e-05 | 0.0295 | 5e-05 | 0.00045 | 8e-05 | 5e-05 | 0.00029
[5 empty] | Averages: |  | 7.5e-05 | 5e-05 | 9e-05 | 0.00080833 | 5.8333e-05 | 6.5e-05 | 0.035017 | 5.3333e-05 | 0.000545 | 8.6667e-05 | 5e-05 | 0.00036833
Transformation to wet weight
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02669.001 | Area i |  | A | 2.751e-05 | 1.965e-05 | 3.93e-05 | 2.751e-05 | 2.751e-05 | 3.144e-05 | 0.013834 | 1.965e-05 | 0.00020436 | 3.537e-05 | 1.965e-05 | 0.00018471
|  |  | MAR02669.002 | Area i |  | B | 5.665e-05 | 2.575e-05 | 6.18e-05 | 4.635e-05 | 4.12e-05 | 4.635e-05 | 0.02714 | 3.605e-05 | 0.00036565 | 6.18e-05 | 2.575e-05 | 0.00028325
|  |  | MAR02669.003 | Area i |  | C | 2.73e-05 | 1.95e-05 | 2.73e-05 | 3.12e-05 | 1.95e-05 | 2.34e-05 | 0.011193 | 1.95e-05 | 0.0001755 | 2.73e-05 | 1.95e-05 | 0.0001209
|  |  | MAR02669.004 | Area ii |  | D | 2.26e-05 | 2.26e-05 | 2.26e-05 | 4.972e-05 | 2.26e-05 | 2.26e-05 | 0.014102 | 2.26e-05 | 0.0002034 | 3.164e-05 | 2.26e-05 | 0.00011752
|  |  | MAR02669.005 | Area ii |  | E | 3.402e-05 | 2.43e-05 | 3.888e-05 | 6.804e-05 | 2.43e-05 | 2.43e-05 | 0.015941 | 2.43e-05 | 0.00033534 | 4.374e-05 | 2.43e-05 | 0.00016038
|  |  | MAR02669.006 | Area ii |  | F | 3.432e-05 | 2.145e-05 | 5.148e-05 | 0.0018704 | 2.145e-05 | 2.574e-05 | 0.012655 | 2.145e-05 | 0.00019305 | 3.432e-05 | 2.145e-05 | 0.00012441
[5 empty] | Averages: |  | 3.3733e-05 | 2.2208e-05 | 4.0227e-05 | 0.00034888 | 2.6093e-05 | 2.8972e-05 | 0.015811 | 2.3925e-05 | 0.00024622 | 3.9028e-05 | 2.2208e-05 | 0.0001652
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02669.001 | Area i |  | A | 2.751e-05 | 1.965e-05 | 3.93e-05 | 2.751e-05 | 2.751e-05 | 3.144e-05 | 0.013834 | 1.965e-05 | 0.00020436 | 3.537e-05 | 1.965e-05 | 0.00018471
|  |  | MAR02669.002 | Area i |  | B | 5.665e-05 | 2.575e-05 | 6.18e-05 | 4.635e-05 | 4.12e-05 | 4.635e-05 | 0.02714 | 3.605e-05 | 0.00036565 | 6.18e-05 | 2.575e-05 | 0.00028325
|  |  | MAR02669.003 | Area i |  | C | 2.73e-05 | 1.95e-05 | 2.73e-05 | 3.12e-05 | 1.95e-05 | 2.34e-05 | 0.011193 | 1.95e-05 | 0.0001755 | 2.73e-05 | 1.95e-05 | 0.0001209
|  |  | MAR02669.004 | Area ii |  | D | 2.26e-05 | 2.26e-05 | 2.26e-05 | 4.972e-05 | 2.26e-05 | 2.26e-05 | 0.014102 | 2.26e-05 | 0.0002034 | 3.164e-05 | 2.26e-05 | 0.00011752
|  |  | MAR02669.005 | Area ii |  | E | 3.402e-05 | 2.43e-05 | 3.888e-05 | 6.804e-05 | 2.43e-05 | 2.43e-05 | 0.015941 | 2.43e-05 | 0.00033534 | 4.374e-05 | 2.43e-05 | 0.00016038
|  |  | MAR02669.006 | Area ii |  | F | 3.432e-05 | 2.145e-05 | 5.148e-05 | 0.0018704 | 2.145e-05 | 2.574e-05 | 0.012655 | 2.145e-05 | 0.00019305 | 3.432e-05 | 2.145e-05 | 0.00012441
[5 empty] | Averages: |  | 3.3733e-05 | 2.2208e-05 | 4.0227e-05 | 0.00034888 | 2.6093e-05 | 2.8972e-05 | 0.015811 | 2.3925e-05 | 0.00024622 | 3.9028e-05 | 2.2208e-05 | 0.0001652
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02669.001 | Area i |  | A | 2.75e-05 | 1.97e-05 | 3.93e-05 | 2.75e-05 | 2.75e-05 | 3.14e-05 | 0.0138 | 1.97e-05 | 0.000204 | 3.54e-05 | 1.97e-05 | 0.000185
|  |  | MAR02669.002 | Area i |  | B | 5.67e-05 | 2.58e-05 | 6.18e-05 | 4.64e-05 | 4.12e-05 | 4.64e-05 | 0.0271 | 3.61e-05 | 0.000366 | 6.18e-05 | 2.58e-05 | 0.000283
|  |  | MAR02669.003 | Area i |  | C | 2.73e-05 | 1.95e-05 | 2.73e-05 | 3.12e-05 | 1.95e-05 | 2.34e-05 | 0.0112 | 1.95e-05 | 0.000176 | 2.73e-05 | 1.95e-05 | 0.000121
|  |  | MAR02669.004 | Area ii |  | D | 2.26e-05 | 2.26e-05 | 2.26e-05 | 4.97e-05 | 2.26e-05 | 2.26e-05 | 0.0141 | 2.26e-05 | 0.000203 | 3.16e-05 | 2.26e-05 | 0.000118
|  |  | MAR02669.005 | Area ii |  | E | 3.4e-05 | 2.43e-05 | 3.89e-05 | 6.8e-05 | 2.43e-05 | 2.43e-05 | 0.0159 | 2.43e-05 | 0.000335 | 4.37e-05 | 2.43e-05 | 0.00016
|  |  | MAR02669.006 | Area ii |  | F | 3.43e-05 | 2.15e-05 | 5.15e-05 | 0.00187 | 2.15e-05 | 2.57e-05 | 0.0127 | 2.15e-05 | 0.000193 | 3.43e-05 | 2.15e-05 | 0.000124
[5 empty] | Averages: |  | 3.3733e-05 | 2.2233e-05 | 4.0233e-05 | 0.0003488 | 2.61e-05 | 2.8967e-05 | 0.0158 | 2.395e-05 | 0.00024617 | 3.9017e-05 | 2.2233e-05 | 0.00016517
Average of dredge areas
[6 empty] | Dredge Area | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[6 empty] | Area i | 3.7167e-05 | 2.1667e-05 | 4.28e-05 | 3.5033e-05 | 2.94e-05 | 3.3733e-05 | 0.017367 | 2.51e-05 | 0.00024867 | 4.15e-05 | 2.1667e-05 | 0.00019633
[6 empty] | Area ii | 3.03e-05 | 2.28e-05 | 3.7667e-05 | 0.00066257 | 2.28e-05 | 2.42e-05 | 0.014233 | 2.28e-05 | 0.00024367 | 3.6533e-05 | 2.28e-05 | 0.000134
Area iii
Area iv
Area v
Area vi
[6 empty] | Averages: | 3.3733e-05 | 2.2233e-05 | 4.0233e-05 | 0.0003488 | 2.61e-05 | 2.8967e-05 | 0.0158 | 2.395e-05 | 0.00024617 | 3.9017e-05 | 2.2233e-05 | 0.00016517
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[6 empty] | Area i | 2.0441e-05 | 1.1917e-05 | 2.354e-05 | 1.9268e-05 | 1.617e-05 | 1.8553e-05 | 0.0095516 | 1.3805e-05 | 0.00013677 | 2.2825e-05 | 1.1917e-05 | 0.00010798
[6 empty] | Area ii | 1.3635e-05 | 1.026e-05 | 1.695e-05 | 0.00029816 | 1.026e-05 | 1.089e-05 | 0.0064051 | 1.026e-05 | 0.00010965 | 1.644e-05 | 1.026e-05 | 6.0301e-05
Area iii
Area iv
Area v
Area vi
PR average
Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[7 empty] | 3.4077e-05 | 2.2177e-05 | 4.049e-05 | 0.00031743 | 2.643e-05 | 2.9443e-05 | 0.015957 | 2.4065e-05 | 0.00024642 | 3.9265e-05 | 2.2177e-05 | 0.00016828

## PR details (hidden)
PR details: |  |  | Dredge area tonnages:
Application number: | SP2504 |  | Dredge Area | Dredging tonnages | % total dredged material | Total dredged material
Date sampled: | 2025-05-07 |  | Area i | 54999 | 55% | 99999
Application title: | DML1955v2 - Marine Application - Barry |  | Area ii | 45000 | 45%
Applicant: | Associated British Ports |  | Area iii
Area iv
Area v
Area vi
PPM (mg/kg)
Metals & Tins | TS% | AS | CD | CR | CU | HG | NI | PB | ZN | DBT | TBT
| 44 | 5.904 | 0.111 | 16.9 | 13.55 | 0.0941 | 14.14 | 27.51 | 93.88
PPB (ug/kg)
Hydrocarbons |  | ACENAPH | ACENAPT | ANTHRAC | BAA | BAP | BBF | BENZGHI | BEP | BKF | C1N | C1PHEN
|  | 48.4 | 37.3 | 91.6 | 249 | 320 | 402 | 302 | 314 | 300 | 322 | 320
Hydrocarbons | C2N | C3N | CHRYSEN | DBENZAH | FLUORAN | FLUOREN | INDPYR | NAPTH | PERYLEN | PHENANT | PYRENE | THC (ppm)
| 261 | 179 | 368 | 71.2 | 483 | 103 | 304 | 167 | 127 | 346 | 380
PPM (mg/kg)
Polychlorinated biphenyls | CB#101 | CB#105 | CB#110 | CB#118 | CB#128 | CB#138 | CB#141 | CB#149 | CB#151
| 0.000948 | 0.000454 | 0.00151 | 0.00125 | 0.00028 | 0.0014 | 0.000268 | 0.00126 | 0.000362
Polychlorinated biphenyls | CB#153 | CB#156 | CB#158 | CB#170 | CB#18 | CB#180 | CB#183 | CB#187 | CB#194
| 0.00187 | 0.000139 | 0.000235 | 0.000578 | 0.0011 | 0.00145 | 0.000252 | 0.000697 | 0.000303
Polychlorinated biphenyls | CB#28 | CB#31 | CB#44 | CB#47 | CB#49 | CB#52 | CB#66 | TOT25CBS | TOTICES7
| 0.00248 | 0.00182 | 0.00102 | 0.000421 | 0.000949 | 0.00107 | 0.00204 | 0.0242 | 0.0105
PPM (mg/kg)
Organochlorine pesticides | AHCH | BHCH | GHCH | DIELDRIN | HCB | PPDDE | PPDDT | PPTDE
| 4.43e-05 | 4.43e-05 | 4.43e-05 | 0.00028 | 0.000133 | 0.000149 | 8.8e-05 | 0.000344
Brominated flame retardants | BDE100 | BDE138 | BDE153 | BDE154 | BDE17 | BDE183 | BDE28 | BDE47
| 3.41e-05 | 2.22e-05 | 4.05e-05 | 0.000317 | 2.64e-05 | 2.94e-05 | 2.41e-05 | 0.000246
Brominated flame retardants | TS%: BDE66; AS: BDE85; CD: BDE99; HG: BDE209
| 3.93e-05 | 2.22e-05 | 0.000168 |  |  | 0.016
PSA | TS%: % Gravel; AS: % Sand; CD: % Silt/Clay
| 44.3017 | 0 | 2.6764

## Import (hidden)
ApplicationNo | TS | Gravel | Sand | Silt | As | Cd | Cr | Cu | Hg | Ni | Pb | Zn | DBT | TBT | Acenapth | Acenapthylene | Antracn | BAA | BAP | BBF | BEP | Benzghip | BKF | C1N | C1PHEN | C2N | C3N | Chrysene | Debenzah | Flurant | Fluorene | Indypr | napth | perylene | phenant | pyrene | THC | PCB28 | PCB52 | PCB101 | PCB118 | PCB138 | PCB153 | PCB18 | PCB105 | PCB110 | PCB128 | PCB141 | PCB149 | PCB151 | PCB156 | PCB158 | PCB170 | PCB180 | PCB183 | PCB187 | PCB194 | PCB31 | PCB44 | PCB47 | PCB49 | PCB66 | ICES7 | AHCH | BHCH | GHCH | DIELDRIN | HCB | DDE | DDT | TDE | BDE100 | BDE138 | BDE153 | BDE154 | BDE17 | BDE183 | BDE209 | BDE28 | BDE47 | BDE66 | BDE85 | BDE99 | Ag | No. exempt from chemical analysis | Tonnes exempt
SP2504 | 44 | 44.3017 | 0 | 2.6764 | 5.904 | 0.111 | 16.9 | 13.55 | 0.0941 | 14.14 | 27.51 | 93.88 |  |  | 48.4 | 37.3 | 91.6 | 249 | 320 | 402 | 314 | 302 | 300 | 322 | 320 | 261 | 179 | 368 | 71.2 | 483 | 103 | 304 | 167 | 127 | 346 | 380 |  | 0.00248 | 0.00107 | 0.000948 | 0.00125 | 0.0014 | 0.00187 | 0.0011 | 0.000454 | 0.00151 | 0.00028 | 0.000268 | 0.00126 | 0.000362 | 0.000139 | 0.000235 | 0.000578 | 0.00145 | 0.000252 | 0.000697 | 0.000303 | 0.00182 | 0.00102 | 0.000421 | 0.000949 | 0.00204 | 0.0105 | 4.43e-05 | 4.43e-05 | 4.43e-05 | 0.00028 | 0.000133 | 0.000149 | 8.8e-05 | 0.000344 | 3.41e-05 | 2.22e-05 | 4.05e-05 | 0.000317 | 2.64e-05 | 2.94e-05 | 0.016 | 2.41e-05 | 0.000246 | 3.93e-05 | 2.22e-05 | 0.000168 |  | 0 | 0