## Application info
Applicant Information
Instructions: |  |  |  |  | Sample numbers and locations
1. All applicants and laboratories should refer to the most recent guidance on sediment analysis in support of marine licence applications on
| the Marine Licensing pages of the NRW website |  |  |  |  | Sample ID | Excluded sample (NRW PS use) | Sample location (decimal degrees, WGS84) |  | Location name (as per sampling plan) | Sampling depth (m) | Dredge area
2. Full information must be provided under each relevant sheet of the workbook. Grey highlighted cells indicate where information can be entered. | [7 empty] | Position latitude | Position longitude
3. Where information cannot be provided, the applicant should consult with NRW PS prior to submission. | [5 empty] | A |  | 51'34.67N | 003'48.78W | Tidal Harbour - A | 10.2 | Area i
4. Worksheets are protected to prevent accidental amendments to calculated values. If amendments are required please consult with NRW PS. | [5 empty] | B |  | 51'34.68N | 003'48.45W | Tidal Harbour - B | 14.9 | Area i
5. Sample IDs used through the data output worksheets should correspond to Sample IDs provided on this worksheet. | [5 empty] | C |  | 51'34.57N | 003'48.07W | Tidal Harbour - C | 10.7 | Area i
[6 empty] | D |  | 51'34.88N | 003'48.78'W | Tidal Harbour - D | 12.9 | Area i
[6 empty] | E |  | 51'34.46N | 003'48.32W | Tidal Harbour - E | 19 | Area i
Marine licence applicant information: | [5 empty] | F |  | 51'34.46N | 003'48.32W | Tidal Harbour - F | 6.4 | Area i
[6 empty] | G |  | 51'34.50N | 003'49.21W | Harbour Approach Channel-G | 13.1 | Area ii
| Applicant: |  | Associated British Ports |  |  | H |  | 51'34.23N | 003'49.99W | Harbour Approach Channel-H | 13.1 | Area ii
| NRW Sample plan reference number: |  | SP2508 |  |  | I |  | 51'34.07N | 003'50.40W | Harbour Approach Channel-I | 13 | Area ii
| Application title: |  | DML1946v2 - Marine Application - Port Talbot |  |  | J |  | 51'33.83N | 003'51.07W | Harbour Approach Channel-J | 12.5 | Area ii
| Date sampled: |  | 2025-05-02 |  |  | K |  | 51'33.52N | 003'51.76W | Harbour Approach Channel-K | 12.1 | Area ii
| Sampling location: |  | Port Talbot |  |  | L |  | 51'33.21N | 003'52.40W | Harbour Approach Channel-L | 12.5 | Area ii
[6 empty] | M |  | 51'34.87N | 003'48.99W | Dock Approach Channel - M | 6.8 | Area iii
[6 empty] | N |  | 51'34.91N | 003'48.69W | Dock Approach Channel - N | 5.3 | Area iii
Dredge area tonnages: | [5 empty] | O |  | 51'34.96N | 003'48.12W | Dock Approach Channel - O | 5.3 | Area iii
[6 empty] | P |  | 51'34.01N | 003'47.96W | Dock Approach Channel - P | 5.5 | Area iii
| Dredge Area | Dredging tonnages | % total dredged material | Total dredged material
| Area i | 2015000 | 65% | 3100000
| Area ii | 930000 | 30%
| Area iii | 155000 | 5%
Area iv
Area v
Area vi
Do not delete
y

## Physical Data
Physical characteristics data
| Instructions: |  |  | Physical characteristics analysis outputs:
1. Record the laboratory/contractor responsible for analysis
| 2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Visual appearance* | Exempt from chemical analysis▫ | Total Solids (% total sediments) | Organic matter (total organic carbon) | Particle size distribution (% at 0.5 phi intervals)
| 3. Enter full dataset for each sample in the analysis results table | [9 empty] | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
| 4. Where copying and pasting entries please use paste values only | [9 empty] | 45mm | 31.5mm | 22.4mm | 16mm | 11.2mm | 8mm | 5.6mm | 4mm | 2.8mm | 2mm | 1.4mm | 1mm | 707µm | 500µm | 353.6µm | 250µm | 176.8µm | 125µm | 88.39µm | 63µm | 44.2µm | 31.3µm | 22.1µm | 15.6µm | 11µm | 7.8µm | 5.5µm | 3.9µm | 2.75µm | 1.95µm | 1.38µm | 0.98µm | 0.69µm | 0.49µm | 0.34µm | 0.24µm | 0.17µm | 0.12µm | 0.09µm | 0.06µm | 0.04µm | <0.04µm
| 5. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.001 | Area i | A | Brown Mud with an Earthy Odour. |  | 42.2 | 2.43 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0003 | 0.48607 | 2.503 | 0.4462 | 0.3065 | 4.7138 | 6.708 | 6.3926 | 8.7749 | 9.7562 | 10.9736 | 12.4646 | 11.2693 | 7.714 | 4.1622 | 2.3734 | 1.8552 | 1.7879 | 1.764 | 1.6466 | 1.4084 | 1.0607 | 0.7662 | 0.46498 | 0.18032 | 0.020992 | 0
|  | IDs should be separated by a comma |  | MAR02655.002 | Area i | B | Brown Mud with an Earthy Odour. |  | 35.6 | 2.34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00016667 | 0.39973 | 2.7991 | 0.67653 | 0.0968 | 3.7863 | 6.6481 | 5.6095 | 8.5564 | 9.0277 | 10.5204 | 12.4495 | 11.4641 | 7.9586 | 4.4404 | 2.6962 | 2.1982 | 2.1179 | 2.0678 | 1.9177 | 1.6393 | 1.2401 | 0.90069 | 0.54954 | 0.2143 | 0.025041 | 0
|  |  |  | MAR02655.003 | Area i | C | Brown Mud with an Earthy Odour. |  | 36.4 | 2.29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.083067 | 1.8775 | 0.9221 | 0.0082 | 1.4982 | 6.2528 | 5.6011 | 7.3093 | 8.7709 | 11.6978 | 13.8839 | 12.5533 | 8.7165 | 4.9446 | 3.0002 | 2.3624 | 2.2006 | 2.1021 | 1.9145 | 1.599 | 1.1729 | 0.82558 | 0.49128 | 0.18982 | 0.022373 | 0
|  |  |  | MAR02655.004 | Area i | D | Brown Mud with an Earthy Odour. |  | 42.4 | 2.35 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013334 | 0.12287 | 0.9564 | 3.5736 | 1.9853 | 0.11333 | 3.044 | 6.7693 | 5.8185 | 7.3888 | 8.5782 | 11.0206 | 12.8706 | 11.5631 | 7.9554 | 4.3419 | 2.4518 | 1.899 | 1.8556 | 1.8503 | 1.7278 | 1.4749 | 1.1149 | 0.80959 | 0.49523 | 0.19573 | 0.023274 | 0
| Analysis information: |  |  | MAR02655.005 | Area i | E | Brown Mud with an Earthy Odour. |  | 44.8 | 2.2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043334 | 0.59517 | 3.3162 | 0.72103 | 0.4765 | 6.1264 | 8.0692 | 7.6367 | 9.2096 | 10.2006 | 11.6786 | 12.1264 | 9.9588 | 6.3956 | 3.2822 | 1.7592 | 1.356 | 1.3519 | 1.36 | 1.2705 | 1.0893 | 0.83717 | 0.61898 | 0.38624 | 0.15796 | 0.019406 | 0
|  |  |  | MAR02655.006 | Area i | F | Odourless Brown Mud. |  | 37.2 | 2.4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.017533 | 0.35923 | 0.498 | 0.11017 | 0.71373 | 1.7745 | 0.20933 | 1.0711 | 6.2281 | 6.3346 | 7.1176 | 9.9614 | 10.8817 | 11.406 | 11.8443 | 10.124 | 6.772 | 3.5409 | 1.8512 | 1.3778 | 1.3889 | 1.4426 | 1.3926 | 1.2295 | 0.96608 | 0.72655 | 0.45628 | 0.1826 | 0.021616 | 0
|  | Laboratory/contractor: | Ocean Ecology Ltd | MAR02655.007 | Area ii | G | Brown Mud with an Earthy Odour. |  | 35.1 | 2.33 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0096667 | 0.5012 | 0.6868 | 0.81903 | 0.2019 | 1.1121 | 1.4852 | 0.79897 | 3.1427 | 5.9515 | 6.9988 | 7.8676 | 10.5066 | 11.8251 | 11.1512 | 10.4575 | 8.5437 | 5.6562 | 2.9524 | 1.5133 | 1.0936 | 1.1077 | 1.1802 | 1.1754 | 1.0755 | 0.87736 | 0.68014 | 0.43495 | 0.17358 | 0.020131 | 0
|  | Date of analysis: | 2025-05-22 | MAR02655.008 | Area ii | H | Brown Mud with an Earthy Odour. |  | 38 | 2.2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0309 | 0.31873 | 0.061433 | 0.012367 | 1.9632 | 4.931 | 4.2476 | 8.1078 | 8.3143 | 10.0224 | 13.2053 | 12.9985 | 9.3123 | 5.4846 | 3.6466 | 3.0017 | 2.7632 | 2.6824 | 2.5702 | 2.2682 | 1.7327 | 1.2494 | 0.75258 | 0.28904 | 0.033462 | 0
|  |  |  | MAR02655.009 | Area ii | I | Brown Mud with an Earthy Odour. |  | 48.4 | 2.08 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0021667 | 1.4632 | 4.9456 | 0.59047 | 1.0492 | 6.4844 | 8.2045 | 9.1265 | 10.3693 | 10.2997 | 10.26 | 10.181 | 8.3763 | 5.477 | 2.8961 | 1.6402 | 1.3377 | 1.3605 | 1.3734 | 1.2886 | 1.1196 | 0.8785 | 0.66417 | 0.42033 | 0.17087 | 0.020525 | 0
|  |  |  | MAR02655.010 | Area ii | J | Brown Mud with an Earthy Odour. |  | 44.8 | 2.25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0053667 | 1.4492 | 5.3783 | 1.2424 | 0.6845 | 6.2835 | 8.5795 | 9.2035 | 10.1339 | 10.1969 | 10.487 | 10.177 | 8.1452 | 5.2928 | 2.8521 | 1.6414 | 1.3144 | 1.3068 | 1.3043 | 1.2179 | 1.0568 | 0.83121 | 0.62991 | 0.40052 | 0.16539 | 0.020246 | 0
|  |  |  | MAR02655.011 | Area ii | K | Brown Mud with an Earthy Odour. |  | 47 | 1.71 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0025333 | 0.93323 | 2.5238 | 0.29703 | 2.7814 | 8.6442 | 10.01 | 10.3225 | 10.5183 | 9.7762 | 9.4126 | 9.2532 | 7.6597 | 5.0925 | 2.7546 | 1.5859 | 1.2969 | 1.3205 | 1.3367 | 1.2581 | 1.097 | 0.86402 | 0.65555 | 0.41544 | 0.1682 | 0.020048 | 0
|  |  |  | MAR02655.012 | Area ii | L | Brown Mud with an Earthy Odour. |  | 52.1 | 1.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015333 | 1.0509 | 3.6678 | 0.5233 | 2.7467 | 8.4675 | 10.4786 | 10.5043 | 10.1139 | 9.7633 | 9.7068 | 9.1711 | 7.2883 | 4.8105 | 2.6687 | 1.5508 | 1.2096 | 1.1769 | 1.1683 | 1.094 | 0.95625 | 0.75903 | 0.58002 | 0.37049 | 0.15273 | 0.018552 | 0
|  |  |  | MAR02655.013 | Area iii | M | Brown Mud with an Earthy Odour. |  | 69.9 | 0.39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.96573 | 11.171 | 30.8701 | 30.237 | 10.4167 | 4.7747 | 1.9803 | 1.213 | 0.78497 | 0.94209 | 1.4133 | 1.4717 | 1.1305 | 0.66204 | 0.39194 | 0.37773 | 0.39349 | 0.3269 | 0.22545 | 0.13536 | 0.071449 | 0.030427 | 0.011346 | 0.0026033 | 0.0001508 | 5e-08 | 0
|  |  |  | MAR02655.014 | Area iii | N | Brown Mud with Organic Matter and an Earthy Odour. |  | 70.8 | 0.41 | 0 | 0 | 0 | 0 | 0 | 0 | 0.005419 | 0.010838 | 0.021676 | 0.054189 | 0.070445 | 0.075864 | 0 | 0 | 0.19643 | 0.83933 | 1.7853 | 6.9972 | 1.7083 | 2.6908 | 8.0277 | 8.8369 | 7.8574 | 7.9264 | 8.5356 | 9.6829 | 9.8973 | 8.0368 | 5.1536 | 2.721 | 1.5718 | 1.265 | 1.2267 | 1.1851 | 1.0739 | 0.90284 | 0.68516 | 0.50353 | 0.31266 | 0.12651 | 0.015351 | 0
|  |  |  | MAR02655.015 | Area iii | O | Brown Mud with Organic Matter and an Earthy Odour. |  | 48 | 4.67 | 0 | 0 | 0 | 0 | 0 | 0.086078 | 0.017216 | 0.028693 | 0.011477 | 0.04017 | 0.057386 | 0.068863 | 1.3775 | 1.499 | 2.3053 | 1.1278 | 1.6812 | 6.059 | 2.0239 | 3.6053 | 8.003 | 7.9383 | 7.1552 | 8.1727 | 8.3861 | 8.7579 | 8.9819 | 7.4519 | 4.8026 | 2.4386 | 1.303 | 1.0323 | 1.0522 | 1.0654 | 0.99698 | 0.85861 | 0.66494 | 0.49653 | 0.3115 | 0.12627 | 0.015223 | 0
|  |  |  | MAR02655.016 | Area iii | P | Brown Mud with an Earthy Odour. |  | 45.5 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.9105 | 11.4125 | 31.1979 | 30.6115 | 10.4728 | 4.5921 | 1.9279 | 1.0597 | 0.78839 | 0.81653 | 1.2313 | 1.3753 | 1.0773 | 0.62937 | 0.37649 | 0.36427 | 0.3778 | 0.31409 | 0.21785 | 0.13195 | 0.070296 | 0.030003 | 0.011338 | 0.0026727 | 0.0001746 | 2.8e-07 | 0
* Visual appearance: Incude a description of what the material looks like and what it contains, e.g. sandy material containing brick fragments, or black silt, or foreign man made matter caught in the sample.
▫ Exempt from chemical analysis: enter 'y' where sediment samples contain glacial material or are too coarse and thus exempt from chemical analysis.
y

## Physical Stats (hidden)
Physical characteristics summary
Physical characteristics statistics:
Analysis information: |  |  |  | Laboratory sample number | Dredge Area | Sample ID | Excluded (y if yes) | Visual appearance | Exempt from chemical analysis | Dry matter (% total sediments) | Organic matter (total organic carbon) |  | Particle size distribution (% at 0.5 phi intervals) | [40 empty] | Particle size summary statistics
[12 empty] | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5 | Gravel (%) | Sand (%) | Very coarse and coarse sand (%) | Medium sand (%) | Fine sand and very fine sand (%) | Silt/Clay (%)
| Applicant: | Associated British Ports | [9 empty] | 45mm | 31.5mm | 22.4mm | 16mm | 11.2mm | 8mm | 5.6mm | 4mm | 2.8mm | 2mm | 1.4mm | 1mm | 707µm | 500µm | 353.6µm | 250µm | 176.8µm | 125µm | 88.39µm | 63µm | 44.2µm | 31.3µm | 22.1µm | 15.6µm | 11µm | 7.8µm | 5.5µm | 3.9µm | 2.75µm | 1.95µm | 1.38µm | 0.98µm | 0.69µm | 0.49µm | 0.34µm | 0.24µm | 0.17µm | 0.12µm | 0.09µm | 0.06µm | 0.04µm | <0.04µm
| Application number: | SP2508 |  | MAR02655.001 | Area i | A |  | Brown Mud with an Earthy Odour. |  | 42.2 | 2.43 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0003 | 0.48607 | 2.503 | 0.4462 | 0.3065 | 4.7138 | 6.708 | 6.3926 | 8.7749 | 9.7562 | 10.9736 | 12.4646 | 11.2693 | 7.714 | 4.1622 | 2.3734 | 1.8552 | 1.7879 | 1.764 | 1.6466 | 1.4084 | 1.0607 | 0.7662 | 0.46498 | 0.18032 | 0.020992 | 0 | 0 | 3.7421 | 0 | 0.0003 | 3.7418 | 96.2579
| Application title: | DML1946v2 - Marine Application - Port Talbot |  | MAR02655.002 | Area i | B |  | Brown Mud with an Earthy Odour. |  | 35.6 | 2.34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00016667 | 0.39973 | 2.7991 | 0.67653 | 0.0968 | 3.7863 | 6.6481 | 5.6095 | 8.5564 | 9.0277 | 10.5204 | 12.4495 | 11.4641 | 7.9586 | 4.4404 | 2.6962 | 2.1982 | 2.1179 | 2.0678 | 1.9177 | 1.6393 | 1.2401 | 0.90069 | 0.54954 | 0.2143 | 0.025041 | 0 | 0 | 3.9723 | 0 | 0.00016667 | 3.9722 | 96.0277
| Date sampled: | 2025-05-02 |  | MAR02655.003 | Area i | C |  | Brown Mud with an Earthy Odour. |  | 36.4 | 2.29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.083067 | 1.8775 | 0.9221 | 0.0082 | 1.4982 | 6.2528 | 5.6011 | 7.3093 | 8.7709 | 11.6978 | 13.8839 | 12.5533 | 8.7165 | 4.9446 | 3.0002 | 2.3624 | 2.2006 | 2.1021 | 1.9145 | 1.599 | 1.1729 | 0.82558 | 0.49128 | 0.18982 | 0.022373 | 0 | 0 | 2.8909 | 0 | 0 | 2.8909 | 97.1091
| Sampling location: | Port Talbot |  | MAR02655.004 | Area i | D |  | Brown Mud with an Earthy Odour. |  | 42.4 | 2.35 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013334 | 0.12287 | 0.9564 | 3.5736 | 1.9853 | 0.11333 | 3.044 | 6.7693 | 5.8185 | 7.3888 | 8.5782 | 11.0206 | 12.8706 | 11.5631 | 7.9554 | 4.3419 | 2.4518 | 1.899 | 1.8556 | 1.8503 | 1.7278 | 1.4749 | 1.1149 | 0.80959 | 0.49523 | 0.19573 | 0.023274 | 0 | 0 | 6.7516 | 0 | 0.123 | 6.6286 | 93.2484
|  |  |  | MAR02655.005 | Area i | E |  | Brown Mud with an Earthy Odour. |  | 44.8 | 2.2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043334 | 0.59517 | 3.3162 | 0.72103 | 0.4765 | 6.1264 | 8.0692 | 7.6367 | 9.2096 | 10.2006 | 11.6786 | 12.1264 | 9.9588 | 6.3956 | 3.2822 | 1.7592 | 1.356 | 1.3519 | 1.36 | 1.2705 | 1.0893 | 0.83717 | 0.61898 | 0.38624 | 0.15796 | 0.019406 | 0 | 0 | 5.1093 | 0 | 0.00043334 | 5.1089 | 94.8907
| Laboratory/contractor: | Ocean Ecology Ltd |  | MAR02655.006 | Area i | F |  | Odourless Brown Mud. |  | 37.2 | 2.4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.017533 | 0.35923 | 0.498 | 0.11017 | 0.71373 | 1.7745 | 0.20933 | 1.0711 | 6.2281 | 6.3346 | 7.1176 | 9.9614 | 10.8817 | 11.406 | 11.8443 | 10.124 | 6.772 | 3.5409 | 1.8512 | 1.3778 | 1.3889 | 1.4426 | 1.3926 | 1.2295 | 0.96608 | 0.72655 | 0.45628 | 0.1826 | 0.021616 | 0 | 0 | 4.7536 | 0.37677 | 0.60817 | 3.7686 | 95.2464
| Date of analysis: | 2025-05-22 |  | MAR02655.007 | Area ii | G |  | Brown Mud with an Earthy Odour. |  | 35.1 | 2.33 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0096667 | 0.5012 | 0.6868 | 0.81903 | 0.2019 | 1.1121 | 1.4852 | 0.79897 | 3.1427 | 5.9515 | 6.9988 | 7.8676 | 10.5066 | 11.8251 | 11.1512 | 10.4575 | 8.5437 | 5.6562 | 2.9524 | 1.5133 | 1.0936 | 1.1077 | 1.1802 | 1.1754 | 1.0755 | 0.87736 | 0.68014 | 0.43495 | 0.17358 | 0.020131 | 0 | 0 | 8.7575 | 1.1977 | 1.0209 | 6.5389 | 91.2425
|  |  |  | MAR02655.008 | Area ii | H |  | Brown Mud with an Earthy Odour. |  | 38 | 2.2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0309 | 0.31873 | 0.061433 | 0.012367 | 1.9632 | 4.931 | 4.2476 | 8.1078 | 8.3143 | 10.0224 | 13.2053 | 12.9985 | 9.3123 | 5.4846 | 3.6466 | 3.0017 | 2.7632 | 2.6824 | 2.5702 | 2.2682 | 1.7327 | 1.2494 | 0.75258 | 0.28904 | 0.033462 | 0 | 0 | 0.42343 | 0 | 0 | 0.42343 | 99.5766
|  |  |  | MAR02655.009 | Area ii | I |  | Brown Mud with an Earthy Odour. |  | 48.4 | 2.08 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0021667 | 1.4632 | 4.9456 | 0.59047 | 1.0492 | 6.4844 | 8.2045 | 9.1265 | 10.3693 | 10.2997 | 10.26 | 10.181 | 8.3763 | 5.477 | 2.8961 | 1.6402 | 1.3377 | 1.3605 | 1.3734 | 1.2886 | 1.1196 | 0.8785 | 0.66417 | 0.42033 | 0.17087 | 0.020525 | 0 | 0 | 8.0507 | 0 | 0.0021667 | 8.0485 | 91.9493
|  |  |  | MAR02655.010 | Area ii | J |  | Brown Mud with an Earthy Odour. |  | 44.8 | 2.25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0053667 | 1.4492 | 5.3783 | 1.2424 | 0.6845 | 6.2835 | 8.5795 | 9.2035 | 10.1339 | 10.1969 | 10.487 | 10.177 | 8.1452 | 5.2928 | 2.8521 | 1.6414 | 1.3144 | 1.3068 | 1.3043 | 1.2179 | 1.0568 | 0.83121 | 0.62991 | 0.40052 | 0.16539 | 0.020246 | 0 | 0 | 8.7597 | 0 | 0.0053667 | 8.7543 | 91.2403
|  |  |  | MAR02655.011 | Area ii | K |  | Brown Mud with an Earthy Odour. |  | 47 | 1.71 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0025333 | 0.93323 | 2.5238 | 0.29703 | 2.7814 | 8.6442 | 10.01 | 10.3225 | 10.5183 | 9.7762 | 9.4126 | 9.2532 | 7.6597 | 5.0925 | 2.7546 | 1.5859 | 1.2969 | 1.3205 | 1.3367 | 1.2581 | 1.097 | 0.86402 | 0.65555 | 0.41544 | 0.1682 | 0.020048 | 0 | 0 | 6.538 | 0 | 0.0025333 | 6.5354 | 93.462
|  |  |  | MAR02655.012 | Area ii | L |  | Brown Mud with an Earthy Odour. |  | 52.1 | 1.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015333 | 1.0509 | 3.6678 | 0.5233 | 2.7467 | 8.4675 | 10.4786 | 10.5043 | 10.1139 | 9.7633 | 9.7068 | 9.1711 | 7.2883 | 4.8105 | 2.6687 | 1.5508 | 1.2096 | 1.1769 | 1.1683 | 1.094 | 0.95625 | 0.75903 | 0.58002 | 0.37049 | 0.15273 | 0.018552 | 0 | 0 | 7.9902 | 0 | 0.0015333 | 7.9887 | 92.0098
|  |  |  | MAR02655.013 | Area iii | M |  | Brown Mud with an Earthy Odour. |  | 69.9 | 0.39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.96573 | 11.171 | 30.8701 | 30.237 | 10.4167 | 4.7747 | 1.9803 | 1.213 | 0.78497 | 0.94209 | 1.4133 | 1.4717 | 1.1305 | 0.66204 | 0.39194 | 0.37773 | 0.39349 | 0.3269 | 0.22545 | 0.13536 | 0.071449 | 0.030427 | 0.011346 | 0.0026033 | 0.0001508 | 5e-08 | 0 | 0 | 83.6605 | 0 | 0.96573 | 82.6948 | 16.3395
|  |  |  | MAR02655.014 | Area iii | N |  | Brown Mud with Organic Matter and an Earthy Odour. |  | 70.8 | 0.41 | 0 | 0 | 0 | 0 | 0 | 0 | 0.005419 | 0.010838 | 0.021676 | 0.054189 | 0.070445 | 0.075864 | 0 | 0 | 0.19643 | 0.83933 | 1.7853 | 6.9972 | 1.7083 | 2.6908 | 8.0277 | 8.8369 | 7.8574 | 7.9264 | 8.5356 | 9.6829 | 9.8973 | 8.0368 | 5.1536 | 2.721 | 1.5718 | 1.265 | 1.2267 | 1.1851 | 1.0739 | 0.90284 | 0.68516 | 0.50353 | 0.31266 | 0.12651 | 0.015351 | 0 | 0.092122 | 14.3637 | 0.14631 | 1.0358 | 13.1816 | 85.5442
|  |  |  | MAR02655.015 | Area iii | O |  | Brown Mud with Organic Matter and an Earthy Odour. |  | 48 | 4.67 | 0 | 0 | 0 | 0 | 0 | 0.086078 | 0.017216 | 0.028693 | 0.011477 | 0.04017 | 0.057386 | 0.068863 | 1.3775 | 1.499 | 2.3053 | 1.1278 | 1.6812 | 6.059 | 2.0239 | 3.6053 | 8.003 | 7.9383 | 7.1552 | 8.1727 | 8.3861 | 8.7579 | 8.9819 | 7.4519 | 4.8026 | 2.4386 | 1.303 | 1.0323 | 1.0522 | 1.0654 | 0.99698 | 0.85861 | 0.66494 | 0.49653 | 0.3115 | 0.12627 | 0.015223 | 0 | 0.18363 | 19.8053 | 3.0028 | 3.4332 | 13.3694 | 80.011
|  |  |  | MAR02655.016 | Area iii | P |  | Brown Mud with an Earthy Odour. |  | 45.5 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.9105 | 11.4125 | 31.1979 | 30.6115 | 10.4728 | 4.5921 | 1.9279 | 1.0597 | 0.78839 | 0.81653 | 1.2313 | 1.3753 | 1.0773 | 0.62937 | 0.37649 | 0.36427 | 0.3778 | 0.31409 | 0.21785 | 0.13195 | 0.070296 | 0.030003 | 0.011338 | 0.0026727 | 0.0001746 | 2.8e-07 | 0 | 0 | 84.6052 | 0 | 0.9105 | 83.6947 | 15.3948
|  |  |  | Averages: | [5 empty] | 46.1375 | 2.2719 | 0 | 0 | 0 | 0 | 0 | 0.0053799 | 0.0014147 | 0.0024707 | 0.0020721 | 0.0058974 | 0.0079894 | 0.0096496 | 0.11852 | 0.15906 | 0.23868 | 0.26818 | 2.2077 | 6.8305 | 4.5659 | 2.4797 | 5.5368 | 6.9167 | 6.6708 | 8.0389 | 8.5044 | 9.3389 | 9.9882 | 8.6025 | 5.7751 | 3.1405 | 1.8329 | 1.4607 | 1.4161 | 1.3954 | 1.3008 | 1.1198 | 0.85907 | 0.6331 | 0.39171 | 0.15585 | 0.018515 | 0 | 0.017235 | 16.8859 | 0.29522 | 0.50686 | 16.0838 | 83.0969
Removal of excluded areas
|  |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Excluded (y if yes) | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
|  |  |  | MAR02655.001 | Area i | A |  | 42.2 |  | 0 | 3.7421 | 96.2579
|  |  |  | MAR02655.002 | Area i | B |  | 35.6 |  | 0 | 3.9723 | 96.0277
|  |  |  | MAR02655.003 | Area i | C |  | 36.4 |  | 0 | 2.8909 | 97.1091
|  |  |  | MAR02655.004 | Area i | D |  | 42.4 |  | 0 | 6.7516 | 93.2484
|  |  |  | MAR02655.005 | Area i | E |  | 44.8 |  | 0 | 5.1093 | 94.8907
|  |  |  | MAR02655.006 | Area i | F |  | 37.2 |  | 0 | 4.7536 | 95.2464
|  |  |  | MAR02655.007 | Area ii | G |  | 35.1 |  | 0 | 8.7575 | 91.2425
|  |  |  | MAR02655.008 | Area ii | H |  | 38 |  | 0 | 0.42343 | 99.5766
|  |  |  | MAR02655.009 | Area ii | I |  | 48.4 |  | 0 | 8.0507 | 91.9493
|  |  |  | MAR02655.010 | Area ii | J |  | 44.8 |  | 0 | 8.7597 | 91.2403
|  |  |  | MAR02655.011 | Area ii | K |  | 47 |  | 0 | 6.538 | 93.462
|  |  |  | MAR02655.012 | Area ii | L |  | 52.1 |  | 0 | 7.9902 | 92.0098
|  |  |  | MAR02655.013 | Area iii | M |  | 69.9 |  | 0 | 83.6605 | 16.3395
|  |  |  | MAR02655.014 | Area iii | N |  | 70.8 |  | 0.092122 | 14.3637 | 85.5442
|  |  |  | MAR02655.015 | Area iii | O |  | 48 |  | 0.18363 | 19.8053 | 80.011
|  |  |  | MAR02655.016 | Area iii | P |  | 45.5 |  | 0 | 84.6052 | 15.3948
|  |  |  | Averages: |  |  |  | 46.1375 |  | 0.017235 | 16.8859 | 83.0969
Average of dredge areas
[7 empty] | Dredge area | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[7 empty] | Area i | 39.7667 |  | 0 | 4.5366 | 95.4634
[7 empty] | Area ii | 44.2333 |  | 0 | 6.7533 | 93.2467
[7 empty] | Area iii | 58.55 |  | 0.068939 | 50.6087 | 49.3224
Area iv
Area v
Area vi
PR weightings (dredge area averages multiplied by proportion of total tonnages)
[7 empty] | Dredge area | Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[7 empty] | Area i | 25.8483 |  | 0 | 2.9488 | 62.0512
[7 empty] | Area ii | 13.27 |  | 0 | 2.026 | 27.974
[7 empty] | Area iii | 2.9275 |  | 0.003447 | 2.5304 | 2.4661
Area iv
Area v
Area vi
PR average
Particle size summary statistics
[8 empty] | Total solids (%) |  | Gravel (%) | Sand (%) | Silt/Clay (%)
[8 empty] | 42.0458 |  | 0.003447 | 7.5052 | 92.4913

## PSA charts (hidden)
| LSN | 45000 | 31500 | 22400 | 16000 | 11200 | 8000 | 5600 | 4000 | 2800 | 2000 | 1400 | 1000 | 707 | 500 | 353.6 | 250 | 176.8 | 125 | 88.39 | 63 | 44.2 | 31.3 | 22.1 | 15.6 | 11 | 7.8 | 5.5 | 3.9 | 2.75 | 1.95 | 1.38 | 0.98 | 0.69 | 0.49 | 0.34 | 0.24 | 0.17 | 0.12 | 0.09 | 0.06 | 0.04 | 0
x-axis (phi) |  | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
[44 empty] | Area |  | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | >14.5
y-axis | A | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0003 | 0.48607 | 2.503 | 0.4462 | 0.3065 | 4.7138 | 6.708 | 6.3926 | 8.7749 | 9.7562 | 10.9736 | 12.4646 | 11.2693 | 7.714 | 4.1622 | 2.3734 | 1.8552 | 1.7879 | 1.764 | 1.6466 | 1.4084 | 1.0607 | 0.7662 | 0.46498 | 0.18032 | 0.020992 | 0 | Area i | Area i | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0029222 | 0.059872 | 0.083022 | 0.038989 | 0.53903 | 2.6407 | 0.82674 | 0.34541 | 4.2328 | 6.797 | 6.3627 | 8.5334 | 9.5359 | 11.2162 | 12.6066 | 11.1554 | 7.5854 | 4.1187 | 2.3553 | 1.8414 | 1.7838 | 1.7645 | 1.6449 | 1.4067 | 1.0653 | 0.7746 | 0.47393 | 0.18679 | 0.022117 | 0
| B | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00016667 | 0.39973 | 2.7991 | 0.67653 | 0.0968 | 3.7863 | 6.6481 | 5.6095 | 8.5564 | 9.0277 | 10.5204 | 12.4495 | 11.4641 | 7.9586 | 4.4404 | 2.6962 | 2.1982 | 2.1179 | 2.0678 | 1.9177 | 1.6393 | 1.2401 | 0.90069 | 0.54954 | 0.2143 | 0.025041 | 0 | Area i | Area ii | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0016111 | 0.083533 | 0.11447 | 0.13651 | 0.035583 | 1.0066 | 3.0532 | 0.58559 | 1.7361 | 6.299 | 8.2004 | 8.5453 | 9.9583 | 10.0293 | 10.1733 | 10.4075 | 8.8353 | 5.9402 | 3.2681 | 1.9297 | 1.5423 | 1.506 | 1.5075 | 1.434 | 1.2622 | 0.99047 | 0.7432 | 0.46572 | 0.18663 | 0.022161 | 0
| C | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.083067 | 1.8775 | 0.9221 | 0.0082 | 1.4982 | 6.2528 | 5.6011 | 7.3093 | 8.7709 | 11.6978 | 13.8839 | 12.5533 | 8.7165 | 4.9446 | 3.0002 | 2.3624 | 2.2006 | 2.1021 | 1.9145 | 1.599 | 1.1729 | 0.82558 | 0.49128 | 0.18982 | 0.022373 | 0 | Area i | Area iii | 0 | 0 | 0 | 0 | 0 | 0.02152 | 0.0056587 | 0.0098827 | 0.0082883 | 0.02359 | 0.031958 | 0.036182 | 0.34439 | 0.37474 | 0.62544 | 0.96085 | 6.5125 | 18.781 | 16.1452 | 6.7964 | 6.3494 | 5.1709 | 4.3213 | 4.4181 | 4.6701 | 5.2714 | 5.4316 | 4.4241 | 2.8119 | 1.482 | 0.9042 | 0.76713 | 0.72996 | 0.67346 | 0.58454 | 0.4758 | 0.35263 | 0.25569 | 0.15736 | 0.063275 | 0.0076436 | 0
| D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013334 | 0.12287 | 0.9564 | 3.5736 | 1.9853 | 0.11333 | 3.044 | 6.7693 | 5.8185 | 7.3888 | 8.5782 | 11.0206 | 12.8706 | 11.5631 | 7.9554 | 4.3419 | 2.4518 | 1.899 | 1.8556 | 1.8503 | 1.7278 | 1.4749 | 1.1149 | 0.80959 | 0.49523 | 0.19573 | 0.023274 | 0 | Area i | Area iv
| E | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043334 | 0.59517 | 3.3162 | 0.72103 | 0.4765 | 6.1264 | 8.0692 | 7.6367 | 9.2096 | 10.2006 | 11.6786 | 12.1264 | 9.9588 | 6.3956 | 3.2822 | 1.7592 | 1.356 | 1.3519 | 1.36 | 1.2705 | 1.0893 | 0.83717 | 0.61898 | 0.38624 | 0.15796 | 0.019406 | 0 | Area i | Area v
| F | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.017533 | 0.35923 | 0.498 | 0.11017 | 0.71373 | 1.7745 | 0.20933 | 1.0711 | 6.2281 | 6.3346 | 7.1176 | 9.9614 | 10.8817 | 11.406 | 11.8443 | 10.124 | 6.772 | 3.5409 | 1.8512 | 1.3778 | 1.3889 | 1.4426 | 1.3926 | 1.2295 | 0.96608 | 0.72655 | 0.45628 | 0.1826 | 0.021616 | 0 | Area i | Area vi
| G | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0096667 | 0.5012 | 0.6868 | 0.81903 | 0.2019 | 1.1121 | 1.4852 | 0.79897 | 3.1427 | 5.9515 | 6.9988 | 7.8676 | 10.5066 | 11.8251 | 11.1512 | 10.4575 | 8.5437 | 5.6562 | 2.9524 | 1.5133 | 1.0936 | 1.1077 | 1.1802 | 1.1754 | 1.0755 | 0.87736 | 0.68014 | 0.43495 | 0.17358 | 0.020131 | 0 | Area ii
| H | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0309 | 0.31873 | 0.061433 | 0.012367 | 1.9632 | 4.931 | 4.2476 | 8.1078 | 8.3143 | 10.0224 | 13.2053 | 12.9985 | 9.3123 | 5.4846 | 3.6466 | 3.0017 | 2.7632 | 2.6824 | 2.5702 | 2.2682 | 1.7327 | 1.2494 | 0.75258 | 0.28904 | 0.033462 | 0 | Area ii
| I | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0021667 | 1.4632 | 4.9456 | 0.59047 | 1.0492 | 6.4844 | 8.2045 | 9.1265 | 10.3693 | 10.2997 | 10.26 | 10.181 | 8.3763 | 5.477 | 2.8961 | 1.6402 | 1.3377 | 1.3605 | 1.3734 | 1.2886 | 1.1196 | 0.8785 | 0.66417 | 0.42033 | 0.17087 | 0.020525 | 0 | Area ii
| J | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0053667 | 1.4492 | 5.3783 | 1.2424 | 0.6845 | 6.2835 | 8.5795 | 9.2035 | 10.1339 | 10.1969 | 10.487 | 10.177 | 8.1452 | 5.2928 | 2.8521 | 1.6414 | 1.3144 | 1.3068 | 1.3043 | 1.2179 | 1.0568 | 0.83121 | 0.62991 | 0.40052 | 0.16539 | 0.020246 | 0 | Area ii
| K | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0025333 | 0.93323 | 2.5238 | 0.29703 | 2.7814 | 8.6442 | 10.01 | 10.3225 | 10.5183 | 9.7762 | 9.4126 | 9.2532 | 7.6597 | 5.0925 | 2.7546 | 1.5859 | 1.2969 | 1.3205 | 1.3367 | 1.2581 | 1.097 | 0.86402 | 0.65555 | 0.41544 | 0.1682 | 0.020048 | 0 | Area ii
| L | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0015333 | 1.0509 | 3.6678 | 0.5233 | 2.7467 | 8.4675 | 10.4786 | 10.5043 | 10.1139 | 9.7633 | 9.7068 | 9.1711 | 7.2883 | 4.8105 | 2.6687 | 1.5508 | 1.2096 | 1.1769 | 1.1683 | 1.094 | 0.95625 | 0.75903 | 0.58002 | 0.37049 | 0.15273 | 0.018552 | 0 | Area ii
| M | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.96573 | 11.171 | 30.8701 | 30.237 | 10.4167 | 4.7747 | 1.9803 | 1.213 | 0.78497 | 0.94209 | 1.4133 | 1.4717 | 1.1305 | 0.66204 | 0.39194 | 0.37773 | 0.39349 | 0.3269 | 0.22545 | 0.13536 | 0.071449 | 0.030427 | 0.011346 | 0.0026033 | 0.0001508 | 5e-08 | 0 | Area iii
| N | 0 | 0 | 0 | 0 | 0 | 0 | 0.005419 | 0.010838 | 0.021676 | 0.054189 | 0.070445 | 0.075864 | 0 | 0 | 0.19643 | 0.83933 | 1.7853 | 6.9972 | 1.7083 | 2.6908 | 8.0277 | 8.8369 | 7.8574 | 7.9264 | 8.5356 | 9.6829 | 9.8973 | 8.0368 | 5.1536 | 2.721 | 1.5718 | 1.265 | 1.2267 | 1.1851 | 1.0739 | 0.90284 | 0.68516 | 0.50353 | 0.31266 | 0.12651 | 0.015351 | 0 | Area iii
| O | 0 | 0 | 0 | 0 | 0 | 0.086078 | 0.017216 | 0.028693 | 0.011477 | 0.04017 | 0.057386 | 0.068863 | 1.3775 | 1.499 | 2.3053 | 1.1278 | 1.6812 | 6.059 | 2.0239 | 3.6053 | 8.003 | 7.9383 | 7.1552 | 8.1727 | 8.3861 | 8.7579 | 8.9819 | 7.4519 | 4.8026 | 2.4386 | 1.303 | 1.0323 | 1.0522 | 1.0654 | 0.99698 | 0.85861 | 0.66494 | 0.49653 | 0.3115 | 0.12627 | 0.015223 | 0 | Area iii
| P | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.9105 | 11.4125 | 31.1979 | 30.6115 | 10.4728 | 4.5921 | 1.9279 | 1.0597 | 0.78839 | 0.81653 | 1.2313 | 1.3753 | 1.0773 | 0.62937 | 0.37649 | 0.36427 | 0.3778 | 0.31409 | 0.21785 | 0.13195 | 0.070296 | 0.030003 | 0.011338 | 0.0026727 | 0.0001746 | 2.8e-07 | 0 | Area iii

## Exempt Samples (hidden)
Exempt samples calculations
Exempt samples complete summary
Analysis information: |  |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Excluded (y if yes) | Visual appearance | Exempt from chemical analysis | Conversion to biniomial (hidden column)
| Applicant: | Associated British Ports
| Application number: | SP2508 |  | MAR02655.001 | Area i | A |  | Brown Mud with an Earthy Odour. |  | 0
| Application title: | DML1946v2 - Marine Application - Port Talbot |  | MAR02655.002 | Area i | B |  | Brown Mud with an Earthy Odour. |  | 0
| Date sampled: | 2025-05-02 |  | MAR02655.003 | Area i | C |  | Brown Mud with an Earthy Odour. |  | 0
| Sampling location: | Port Talbot |  | MAR02655.004 | Area i | D |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.005 | Area i | E |  | Brown Mud with an Earthy Odour. |  | 0
| Laboratory/contractor: | Ocean Ecology Ltd |  | MAR02655.006 | Area i | F |  | Odourless Brown Mud. |  | 0
| Date of analysis: | 2025-05-22 |  | MAR02655.007 | Area ii | G |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.008 | Area ii | H |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.009 | Area ii | I |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.010 | Area ii | J |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.011 | Area ii | K |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.012 | Area ii | L |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.013 | Area iii | M |  | Brown Mud with an Earthy Odour. |  | 0
|  |  |  | MAR02655.014 | Area iii | N |  | Brown Mud with Organic Matter and an Earthy Odour. |  | 0
|  |  |  | MAR02655.015 | Area iii | O |  | Brown Mud with Organic Matter and an Earthy Odour. |  | 0
|  |  |  | MAR02655.016 | Area iii | P |  | Brown Mud with an Earthy Odour. |  | 0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Total samples and tonnages exempt
|  |  |  | Dredge Area | Total number tested samples | Number exempt samples | Dredge area tonnages | Proportion exempt samples | Tonnage for OSPAR exempt samples reporting
|  |  |  | Area i | 6 | 0 | 2015000 | 0 | 0
|  |  |  | Area ii | 6 | 0 | 930000 | 0 | 0
|  |  |  | Area iii | 4 | 0 | 155000 | 0 | 0
Area iv
Area v
Area vi
[5 empty] | Total exempt samples: | 0 |  | Total exempt tonnages: | 0

## Trace metal data
Trace metal data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for trace metal analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Metals as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table | [5 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
4. Trace metal analysis results should be reported in mg/kg (ppm) dry weight |  |  | MAR02655.001 | Area i | A | 15.9 | 0.22 | 33.3 | 21.7 | 0.14 | 25.9 | 53.2 | 167
5. Enter methdological limit of detection for each trace metal prior to inputting raw data |  |  | MAR02655.002 | Area i | B | 16.2 | 0.22 | 35.1 | 22.8 | 0.13 | 27.4 | 52.5 | 170
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02655.003 | Area i | C | 16.1 | 0.21 | 34.2 | 22.1 | 0.12 | 26.6 | 53.2 | 172
7. Where copying and pasting entries please use paste values only |  |  | MAR02655.004 | Area i | D | 16.4 | 0.21 | 39 | 24.1 | 0.14 | 29.2 | 55.8 | 179
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.005 | Area i | E | 15.6 | 0.22 | 32.8 | 22 | 0.12 | 25.9 | 51.3 | 166
| IDs should be separated by a comma |  | MAR02655.006 | Area i | F | 16.1 | 0.24 | 35 | 23.9 | 0.16 | 32.6 | 54.3 | 178
|  |  | MAR02655.007 | Area ii | G | 16.1 | 0.18 | 38.2 | 22.1 | 0.23 | 27.3 | 54.2 | 170
|  |  | MAR02655.008 | Area ii | H | 15.6 | 0.16 | 38.1 | 21.8 | 0.12 | 31.6 | 54.7 | 180
|  |  | MAR02655.009 | Area ii | I | 13.7 | 0.19 | 28.6 | 17.8 | 0.14 | 25.6 | 41.5 | 130
Analysis information: |  |  | MAR02655.010 | Area ii | J | 13.6 | 0.2 | 27.4 | 18.3 | 0.12 | 25.9 | 42 | 131
|  |  | MAR02655.011 | Area ii | K | 11.3 | 0.16 | 28.4 | 16.5 | 0.14 | 23 | 38.6 | 128
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.012 | Area ii | L | 11.2 | 0.18 | 27 | 15.7 | 0.12 | 21.8 | 36.1 | 124
| Date of analysis: | 2025-05-28 | MAR02655.013 | Area iii | M | 8.2 | 0.09 | 11.3 | 5.3 | 0.05 | 9 | 16.5 | 69.9
|  |  | MAR02655.014 | Area iii | N | 8.2 | 0.09 | 11.4 | 5.5 | 0.05 | 10 | 17.2 | 70.7
|  |  | MAR02655.015 | Area iii | O | 13.6 | 0.21 | 21.1 | 17.3 | 0.13 | 17.5 | 34.2 | 116
|  |  | MAR02655.016 | Area iii | P | 14.1 | 0.22 | 23.8 | 18 | 0.15 | 19.2 | 35.5 | 123
|  |  | Limits of detection (mg/kg dry weight): |  |  | 0.5 | 0.04 | 0.5 | 0.5 | 0.01 | 0.5 | 0.5 | 2

## Metals and TS Calcs (hidden)
Trace metal summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg dry weight | [7 empty] | Total Solids (%)
| Application number: | SP2508 |  |  |  |  | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
| Application title: | DML1946v2 - Marine Application - Port Talbot | MAR02655.001 | Area i |  | A | 15.9 | 0.22 | 33.3 | 21.7 | 0.14 | 25.9 | 53.2 | 167 | 42.2
| Date sampled: | 2025-05-02 | MAR02655.002 | Area i |  | B | 16.2 | 0.22 | 35.1 | 22.8 | 0.13 | 27.4 | 52.5 | 170 | 35.6
| Sampling location: | Port Talbot | MAR02655.003 | Area i |  | C | 16.1 | 0.21 | 34.2 | 22.1 | 0.12 | 26.6 | 53.2 | 172 | 36.4
|  |  | MAR02655.004 | Area i |  | D | 16.4 | 0.21 | 39 | 24.1 | 0.14 | 29.2 | 55.8 | 179 | 42.4
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.005 | Area i |  | E | 15.6 | 0.22 | 32.8 | 22 | 0.12 | 25.9 | 51.3 | 166 | 44.8
| Date of analysis: | 2025-05-28 | MAR02655.006 | Area i |  | F | 16.1 | 0.24 | 35 | 23.9 | 0.16 | 32.6 | 54.3 | 178 | 37.2
|  |  | MAR02655.007 | Area ii |  | G | 16.1 | 0.18 | 38.2 | 22.1 | 0.23 | 27.3 | 54.2 | 170 | 35.1
|  |  | MAR02655.008 | Area ii |  | H | 15.6 | 0.16 | 38.1 | 21.8 | 0.12 | 31.6 | 54.7 | 180 | 38
|  |  | MAR02655.009 | Area ii |  | I | 13.7 | 0.19 | 28.6 | 17.8 | 0.14 | 25.6 | 41.5 | 130 | 48.4
|  |  | MAR02655.010 | Area ii |  | J | 13.6 | 0.2 | 27.4 | 18.3 | 0.12 | 25.9 | 42 | 131 | 44.8
|  |  | MAR02655.011 | Area ii |  | K | 11.3 | 0.16 | 28.4 | 16.5 | 0.14 | 23 | 38.6 | 128 | 47
|  |  | MAR02655.012 | Area ii |  | L | 11.2 | 0.18 | 27 | 15.7 | 0.12 | 21.8 | 36.1 | 124 | 52.1
|  |  | MAR02655.013 | Area iii |  | M | 8.2 | 0.09 | 11.3 | 5.3 | 0.05 | 9 | 16.5 | 69.9 | 69.9
|  |  | MAR02655.014 | Area iii |  | N | 8.2 | 0.09 | 11.4 | 5.5 | 0.05 | 10 | 17.2 | 70.7 | 70.8
|  |  | MAR02655.015 | Area iii |  | O | 13.6 | 0.21 | 21.1 | 17.3 | 0.13 | 17.5 | 34.2 | 116 | 48
|  |  | MAR02655.016 | Area iii |  | P | 14.1 | 0.22 | 23.8 | 18 | 0.15 | 19.2 | 35.5 | 123 | 45.5
[6 empty] | Averages | 13.8687 | 0.1875 | 29.0438 | 18.4313 | 0.12875 | 23.6562 | 43.175 | 142.1625
[6 empty] | Action level 1: | 20 | 0.4 | 40 | 40 | 0.3 | 20 | 50 | 130
[6 empty] | Action level 2: | 100 | 5 | 400 | 400 | 3 | 200 | 500 | 800
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
|  |  | MAR02655.001 | Area i |  | A | 6.7098 | 0.09284 | 14.0526 | 9.1574 | 0.05908 | 10.9298 | 22.4504 | 70.474 | 42.2
|  |  | MAR02655.002 | Area i |  | B | 5.7672 | 0.07832 | 12.4956 | 8.1168 | 0.04628 | 9.7544 | 18.69 | 60.52 | 35.6
|  |  | MAR02655.003 | Area i |  | C | 5.8604 | 0.07644 | 12.4488 | 8.0444 | 0.04368 | 9.6824 | 19.3648 | 62.608 | 36.4
|  |  | MAR02655.004 | Area i |  | D | 6.9536 | 0.08904 | 16.536 | 10.2184 | 0.05936 | 12.3808 | 23.6592 | 75.896 | 42.4
|  |  | MAR02655.005 | Area i |  | E | 6.9888 | 0.09856 | 14.6944 | 9.856 | 0.05376 | 11.6032 | 22.9824 | 74.368 | 44.8
|  |  | MAR02655.006 | Area i |  | F | 5.9892 | 0.08928 | 13.02 | 8.8908 | 0.05952 | 12.1272 | 20.1996 | 66.216 | 37.2
|  |  | MAR02655.007 | Area ii |  | G | 5.6511 | 0.06318 | 13.4082 | 7.7571 | 0.08073 | 9.5823 | 19.0242 | 59.67 | 35.1
|  |  | MAR02655.008 | Area ii |  | H | 5.928 | 0.0608 | 14.478 | 8.284 | 0.0456 | 12.008 | 20.786 | 68.4 | 38
|  |  | MAR02655.009 | Area ii |  | I | 6.6308 | 0.09196 | 13.8424 | 8.6152 | 0.06776 | 12.3904 | 20.086 | 62.92 | 48.4
|  |  | MAR02655.010 | Area ii |  | J | 6.0928 | 0.0896 | 12.2752 | 8.1984 | 0.05376 | 11.6032 | 18.816 | 58.688 | 44.8
|  |  | MAR02655.011 | Area ii |  | K | 5.311 | 0.0752 | 13.348 | 7.755 | 0.0658 | 10.81 | 18.142 | 60.16 | 47
|  |  | MAR02655.012 | Area ii |  | L | 5.8352 | 0.09378 | 14.067 | 8.1797 | 0.06252 | 11.3578 | 18.8081 | 64.604 | 52.1
|  |  | MAR02655.013 | Area iii |  | M | 5.7318 | 0.06291 | 7.8987 | 3.7047 | 0.03495 | 6.291 | 11.5335 | 48.8601 | 69.9
|  |  | MAR02655.014 | Area iii |  | N | 5.8056 | 0.06372 | 8.0712 | 3.894 | 0.0354 | 7.08 | 12.1776 | 50.0556 | 70.8
|  |  | MAR02655.015 | Area iii |  | O | 6.528 | 0.1008 | 10.128 | 8.304 | 0.0624 | 8.4 | 16.416 | 55.68 | 48
|  |  | MAR02655.016 | Area iii |  | P | 6.4155 | 0.1001 | 10.829 | 8.19 | 0.06825 | 8.736 | 16.1525 | 55.965 | 45.5
[7 empty] | 6.1374 | 0.082908 | 12.5996 | 7.9479 | 0.056178 | 10.296 | 18.7055 | 62.1928 | 46.1375
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
|  |  | MAR02655.001 | Area i |  | A | 6.7098 | 0.09284 | 14.0526 | 9.1574 | 0.05908 | 10.9298 | 22.4504 | 70.474 | 42.2
|  |  | MAR02655.002 | Area i |  | B | 5.7672 | 0.07832 | 12.4956 | 8.1168 | 0.04628 | 9.7544 | 18.69 | 60.52 | 35.6
|  |  | MAR02655.003 | Area i |  | C | 5.8604 | 0.07644 | 12.4488 | 8.0444 | 0.04368 | 9.6824 | 19.3648 | 62.608 | 36.4
|  |  | MAR02655.004 | Area i |  | D | 6.9536 | 0.08904 | 16.536 | 10.2184 | 0.05936 | 12.3808 | 23.6592 | 75.896 | 42.4
|  |  | MAR02655.005 | Area i |  | E | 6.9888 | 0.09856 | 14.6944 | 9.856 | 0.05376 | 11.6032 | 22.9824 | 74.368 | 44.8
|  |  | MAR02655.006 | Area i |  | F | 5.9892 | 0.08928 | 13.02 | 8.8908 | 0.05952 | 12.1272 | 20.1996 | 66.216 | 37.2
|  |  | MAR02655.007 | Area ii |  | G | 5.6511 | 0.06318 | 13.4082 | 7.7571 | 0.08073 | 9.5823 | 19.0242 | 59.67 | 35.1
|  |  | MAR02655.008 | Area ii |  | H | 5.928 | 0.0608 | 14.478 | 8.284 | 0.0456 | 12.008 | 20.786 | 68.4 | 38
|  |  | MAR02655.009 | Area ii |  | I | 6.6308 | 0.09196 | 13.8424 | 8.6152 | 0.06776 | 12.3904 | 20.086 | 62.92 | 48.4
|  |  | MAR02655.010 | Area ii |  | J | 6.0928 | 0.0896 | 12.2752 | 8.1984 | 0.05376 | 11.6032 | 18.816 | 58.688 | 44.8
|  |  | MAR02655.011 | Area ii |  | K | 5.311 | 0.0752 | 13.348 | 7.755 | 0.0658 | 10.81 | 18.142 | 60.16 | 47
|  |  | MAR02655.012 | Area ii |  | L | 5.8352 | 0.09378 | 14.067 | 8.1797 | 0.06252 | 11.3578 | 18.8081 | 64.604 | 52.1
|  |  | MAR02655.013 | Area iii |  | M | 5.7318 | 0.06291 | 7.8987 | 3.7047 | 0.03495 | 6.291 | 11.5335 | 48.8601 | 69.9
|  |  | MAR02655.014 | Area iii |  | N | 5.8056 | 0.06372 | 8.0712 | 3.894 | 0.0354 | 7.08 | 12.1776 | 50.0556 | 70.8
|  |  | MAR02655.015 | Area iii |  | O | 6.528 | 0.1008 | 10.128 | 8.304 | 0.0624 | 8.4 | 16.416 | 55.68 | 48
|  |  | MAR02655.016 | Area iii |  | P | 6.4155 | 0.1001 | 10.829 | 8.19 | 0.06825 | 8.736 | 16.1525 | 55.965 | 45.5
[7 empty] | 6.1374 | 0.082908 | 12.5996 | 7.9479 | 0.056178 | 10.296 | 18.7055 | 62.1928 | 46.1375
Average of dredge areas
[6 empty] | Dredge Area | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[6 empty] | Area i | 6.3782 | 0.087413 | 13.8746 | 9.0473 | 0.053613 | 11.0796 | 21.2244 | 68.347 | 39.7667
[6 empty] | Area ii | 5.9082 | 0.079087 | 13.5698 | 8.1316 | 0.062695 | 11.2919 | 19.2771 | 62.407 | 44.2333
[6 empty] | Area iii | 6.1202 | 0.081883 | 9.2317 | 6.0232 | 0.05025 | 7.6268 | 14.0699 | 52.6402 | 58.55
Area iv
Area v
Area vi
PR weightings (dredge area averages multiplied by proportion of total tonnages)
[6 empty] | Dredge Area | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[6 empty] | Area i | 4.1458 | 0.056819 | 9.0185 | 5.8807 | 0.034849 | 7.2018 | 13.7959 | 44.4256 | 25.8483
[6 empty] | Area ii | 1.7724 | 0.023726 | 4.0709 | 2.4395 | 0.018808 | 3.3876 | 5.7831 | 18.7221 | 13.27
[6 empty] | Area iii | 0.30601 | 0.0040941 | 0.46159 | 0.30116 | 0.0025125 | 0.38134 | 0.7035 | 2.632 | 2.9275
Area iv
Area v
Area vi
PR average
[7 empty] | Metals as mg/kg wet weight | [7 empty] | Total Solids (%)
[7 empty] | Arsenic (As) | Cadmium (Cd) | Chromium (Cr) | Copper (Cu) | Mercury (Hg) | Nickel (Ni) | Lead (Pb) | Zinc (Zn)
[7 empty] | 6.2243 | 0.084639 | 13.551 | 8.6214 | 0.05617 | 10.9707 | 20.2825 | 65.7797 | 42.0458

## Organotins data
Organotin data
Instructions: |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for organotin analysis
2. Record the date the samples were analysed. |  | Laboratory sample number | Dredge Area | Sample ID(s) | Organotins as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table |  |  |  |  | Dibutyltine (DBT) | Tributyltin (TBT)
4. Organotin analysis results should be reported in mg/kg (ppm) dry weight
5. Enter methdological limit of detection for each organotin prior to inputting raw data
6. Where analysis outputs are less than the limits of detection please enter text "<LOD"
7. Where copying and pasting entries please use paste values only
8. Where entering multiple Sample IDs please use the pop-up form
IDs should be separated by a comma
Analysis information:
Laboratory/contractor:
Date of analysis:
Limits of detection (mg/kg dry weight):

## Organotin calcs (hidden)
Organotin summary information
Analysis information: |  |  | Determinand analysis outputs adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg dry weight
| Application number: | SP2508 |  |  |  |  | Dibutyltine (DBT) | Tributyltin (TBT)
| Application title: | DML1946v2 - Marine Application - Port Talbot
| Date sampled: | 2025-05-02
| Sampling location: | Port Talbot
Laboratory/contractor:
Date of analysis:
Averages
[6 empty] | Action level 1: | 0.1 | 0.1
[6 empty] | Action level 2: | 1 | 1
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Average of dredge areas
[6 empty] | Dredge Area | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Area i
Area ii
Area iii
Area iv
Area v
Area vi
Averages:
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)
Area i
Area ii
Area iii
Area iv
Area v
Area vi
Averages:
PR average
Organotins as mg/kg wet weight
[7 empty] | Dibutyltine (DBT) | Tributyltin (TBT)

## PAH data
Polyaromatic hydrocarbon data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for PAH analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | PAHs as dry weight (µg/kg dry weight) | [21 empty] | Total hydrocarbon content (mg/kg)
3. Enter full dataset for each sample in the analysis results table | [5 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
4. Analysis results for individual PAHs should be reported in µg/kg (ppb) dry weight. |  |  | MAR02655.001 | Area i | A | 37.4 | 38.4 | 71.5 | 230 | 284 | 352 | 256 | 263 | 260 | 279 | 286 | 229 | 147 | 330 | 61.4 | 440 | 90.2 | 275 | 155 | 99.8 | 315 | 351
| THC should be reported as mg/kg (ppm) |  | MAR02655.002 | Area i | B | 34.7 | 32.2 | 71.8 | 196 | 250 | 335 | 239 | 243 | 235 | 282 | 281 | 231 | 155 | 304 | 55.7 | 405 | 87.7 | 268 | 169 | 88.5 | 299 | 318
5. Enter methdological limit of detection for each PAH prior to inputting raw data |  |  | MAR02655.003 | Area i | C | 37.8 | 34.8 | 72.7 | 199 | 257 | 349 | 248 | 255 | 246 | 329 | 298 | 261 | 180 | 315 | 59.5 | 402 | 97.4 | 276 | 177 | 90.4 | 314 | 312
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02655.004 | Area i | D | 36.9 | 39.4 | 77.5 | 234 | 286 | 361 | 255 | 265 | 262 | 272 | 264 | 219 | 145 | 336 | 61.9 | 461 | 86.6 | 286 | 164 | 99.6 | 301 | 360
7. Where copying and pasting entries please use paste values only |  |  | MAR02655.005 | Area i | E | 28.1 | 21.7 | 55.1 | 159 | 193 | 255 | 175 | 190 | 189 | 230 | 245 | 200 | 134 | 243 | 37.5 | 340 | 70.1 | 183 | 136 | 71.2 | 257 | 256
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.006 | Area i | F | 37.1 | 27.2 | 68 | 195 | 243 | 331 | 227 | 240 | 230 | 292 | 295 | 250 | 186 | 304 | 49.8 | 400 | 91.4 | 247 | 160 | 85.3 | 309 | 310
| IDs should be separated by a comma |  | MAR02655.007 | Area ii | G | 32.3 | 25.1 | 50.3 | 158 | 203 | 284 | 201 | 207 | 195 | 280 | 254 | 241 | 166 | 256 | 45.4 | 325 | 84.1 | 220 | 145 | 72.8 | 257 | 246
|  |  | MAR02655.008 | Area ii | H | 34.8 | 28.5 | 64 | 185 | 230 | 314 | 222 | 233 | 223 | 294 | 295 | 249 | 171 | 286 | 51.7 | 375 | 88.9 | 238 | 160 | 77.1 | 299 | 283
Analysis information: |  |  | MAR02655.009 | Area ii | I | 25 | 18.9 | 48.6 | 157 | 180 | 220 | 148 | 160 | 160 | 165 | 180 | 145 | 108 | 215 | 35.4 | 312 | 54 | 162 | 91 | 60.7 | 199 | 246
|  |  | MAR02655.010 | Area ii | J | 32.1 | 28.7 | 66.2 | 216 | 241 | 298 | 197 | 216 | 217 | 222 | 221 | 190 | 139 | 289 | 49.3 | 400 | 70.8 | 219 | 126 | 78.4 | 257 | 312
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.011 | Area ii | K | 22.2 | 20.8 | 49.1 | 146 | 169 | 225 | 154 | 163 | 158 | 182 | 206 | 158 | 108 | 217 | 37 | 273 | 57.3 | 171 | 98.6 | 58.8 | 179 | 212
| Date of analysis: | 2025-06-05 | MAR02655.012 | Area ii | L | 15.9 | 13.4 | 29.2 | 87.2 | 105 | 137 | 93.7 | 99.6 | 98.2 | 116 | 112 | 98.3 | 75.8 | 124 | 22.1 | 177 | 37.8 | 103 | 67.9 | 35.3 | 122 | 140
|  |  | MAR02655.013 | Area iii | M | 5.19 | 2.43 | 8.78 | 15.2 | 16.7 | 21.7 | 13.4 | 15.2 | 15.9 | 24.2 | 18.9 | 17.3 | 11.3 | 21.4 | 3.55 | 34.2 | 8.85 | 15.1 | 17.8 | 5.69 | 24.8 | 27.6
|  |  | MAR02655.014 | Area iii | N | 5.31 | 2.86 | 9.68 | 17.6 | 19.5 | 25.3 | 15.8 | 17.4 | 17.9 | 31.2 | 24.8 | 21.5 | 15.1 | 24 | 3.87 | 40.5 | 9.51 | 17.6 | 26.5 | 6.8 | 28.5 | 32.7
|  |  | MAR02655.015 | Area iii | O | 239 | 50.9 | 231 | 739 | 771 | 775 | 483 | 566 | 629 | 387 | 602 | 322 | 230 | 880 | 129 | 1410 | 243 | 545 | 293 | 218 | 1050 | 1140
|  |  | MAR02655.016 | Area iii | P | 93.6 | 32 | 127 | 371 | 394 | 417 | 261 | 302 | 320 | 267 | 330 | 228 | 179 | 449 | 64.9 | 735 | 106 | 292 | 201 | 120 | 503 | 609
|  |  | Limits of detection (µg/kg dry weight): |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## PAH calcs (hidden)
Polyaromatic hydrocarbon summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection and transformed to mg/kg
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as mg/kg dry weight | [21 empty] | Total hydrocarbon content (mg/kg)
| Application number: | SP2508 |  |  |  |  | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
| Application title: | DML1946v2 - Marine Application - Port Talbot | MAR02655.001 | Area i |  | A | 0.0374 | 0.0384 | 0.0715 | 0.23 | 0.284 | 0.352 | 0.256 | 0.263 | 0.26 | 0.279 | 0.286 | 0.229 | 0.147 | 0.33 | 0.0614 | 0.44 | 0.0902 | 0.275 | 0.155 | 0.0998 | 0.315 | 0.351
| Date sampled: | 2025-05-02 | MAR02655.002 | Area i |  | B | 0.0347 | 0.0322 | 0.0718 | 0.196 | 0.25 | 0.335 | 0.239 | 0.243 | 0.235 | 0.282 | 0.281 | 0.231 | 0.155 | 0.304 | 0.0557 | 0.405 | 0.0877 | 0.268 | 0.169 | 0.0885 | 0.299 | 0.318
| Sampling location: | Port Talbot | MAR02655.003 | Area i |  | C | 0.0378 | 0.0348 | 0.0727 | 0.199 | 0.257 | 0.349 | 0.248 | 0.255 | 0.246 | 0.329 | 0.298 | 0.261 | 0.18 | 0.315 | 0.0595 | 0.402 | 0.0974 | 0.276 | 0.177 | 0.0904 | 0.314 | 0.312
|  |  | MAR02655.004 | Area i |  | D | 0.0369 | 0.0394 | 0.0775 | 0.234 | 0.286 | 0.361 | 0.255 | 0.265 | 0.262 | 0.272 | 0.264 | 0.219 | 0.145 | 0.336 | 0.0619 | 0.461 | 0.0866 | 0.286 | 0.164 | 0.0996 | 0.301 | 0.36
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.005 | Area i |  | E | 0.0281 | 0.0217 | 0.0551 | 0.159 | 0.193 | 0.255 | 0.175 | 0.19 | 0.189 | 0.23 | 0.245 | 0.2 | 0.134 | 0.243 | 0.0375 | 0.34 | 0.0701 | 0.183 | 0.136 | 0.0712 | 0.257 | 0.256
| Date of analysis: | 2025-06-05 | MAR02655.006 | Area i |  | F | 0.0371 | 0.0272 | 0.068 | 0.195 | 0.243 | 0.331 | 0.227 | 0.24 | 0.23 | 0.292 | 0.295 | 0.25 | 0.186 | 0.304 | 0.0498 | 0.4 | 0.0914 | 0.247 | 0.16 | 0.0853 | 0.309 | 0.31
|  |  | MAR02655.007 | Area ii |  | G | 0.0323 | 0.0251 | 0.0503 | 0.158 | 0.203 | 0.284 | 0.201 | 0.207 | 0.195 | 0.28 | 0.254 | 0.241 | 0.166 | 0.256 | 0.0454 | 0.325 | 0.0841 | 0.22 | 0.145 | 0.0728 | 0.257 | 0.246
|  |  | MAR02655.008 | Area ii |  | H | 0.0348 | 0.0285 | 0.064 | 0.185 | 0.23 | 0.314 | 0.222 | 0.233 | 0.223 | 0.294 | 0.295 | 0.249 | 0.171 | 0.286 | 0.0517 | 0.375 | 0.0889 | 0.238 | 0.16 | 0.0771 | 0.299 | 0.283
|  |  | MAR02655.009 | Area ii |  | I | 0.025 | 0.0189 | 0.0486 | 0.157 | 0.18 | 0.22 | 0.148 | 0.16 | 0.16 | 0.165 | 0.18 | 0.145 | 0.108 | 0.215 | 0.0354 | 0.312 | 0.054 | 0.162 | 0.091 | 0.0607 | 0.199 | 0.246
|  |  | MAR02655.010 | Area ii |  | J | 0.0321 | 0.0287 | 0.0662 | 0.216 | 0.241 | 0.298 | 0.197 | 0.216 | 0.217 | 0.222 | 0.221 | 0.19 | 0.139 | 0.289 | 0.0493 | 0.4 | 0.0708 | 0.219 | 0.126 | 0.0784 | 0.257 | 0.312
|  |  | MAR02655.011 | Area ii |  | K | 0.0222 | 0.0208 | 0.0491 | 0.146 | 0.169 | 0.225 | 0.154 | 0.163 | 0.158 | 0.182 | 0.206 | 0.158 | 0.108 | 0.217 | 0.037 | 0.273 | 0.0573 | 0.171 | 0.0986 | 0.0588 | 0.179 | 0.212
|  |  | MAR02655.012 | Area ii |  | L | 0.0159 | 0.0134 | 0.0292 | 0.0872 | 0.105 | 0.137 | 0.0937 | 0.0996 | 0.0982 | 0.116 | 0.112 | 0.0983 | 0.0758 | 0.124 | 0.0221 | 0.177 | 0.0378 | 0.103 | 0.0679 | 0.0353 | 0.122 | 0.14
|  |  | MAR02655.013 | Area iii |  | M | 0.00519 | 0.00243 | 0.00878 | 0.0152 | 0.0167 | 0.0217 | 0.0134 | 0.0152 | 0.0159 | 0.0242 | 0.0189 | 0.0173 | 0.0113 | 0.0214 | 0.00355 | 0.0342 | 0.00885 | 0.0151 | 0.0178 | 0.00569 | 0.0248 | 0.0276
|  |  | MAR02655.014 | Area iii |  | N | 0.00531 | 0.00286 | 0.00968 | 0.0176 | 0.0195 | 0.0253 | 0.0158 | 0.0174 | 0.0179 | 0.0312 | 0.0248 | 0.0215 | 0.0151 | 0.024 | 0.00387 | 0.0405 | 0.00951 | 0.0176 | 0.0265 | 0.0068 | 0.0285 | 0.0327
|  |  | MAR02655.015 | Area iii |  | O | 0.239 | 0.0509 | 0.231 | 0.739 | 0.771 | 0.775 | 0.483 | 0.566 | 0.629 | 0.387 | 0.602 | 0.322 | 0.23 | 0.88 | 0.129 | 1.41 | 0.243 | 0.545 | 0.293 | 0.218 | 1.05 | 1.14
|  |  | MAR02655.016 | Area iii |  | P | 0.0936 | 0.032 | 0.127 | 0.371 | 0.394 | 0.417 | 0.261 | 0.302 | 0.32 | 0.267 | 0.33 | 0.228 | 0.179 | 0.449 | 0.0649 | 0.735 | 0.106 | 0.292 | 0.201 | 0.12 | 0.503 | 0.609
[5 empty] | Averages: |  | 0.044838 | 0.026081 | 0.068779 | 0.20656 | 0.24014 | 0.29375 | 0.19931 | 0.2147 | 0.216 | 0.22828 | 0.24454 | 0.19126 | 0.13439 | 0.28709 | 0.048001 | 0.40811 | 0.080229 | 0.21986 | 0.13674 | 0.079274 | 0.29464 | 0.32221
[6 empty] | Action level 1: | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.01 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 100
Transformation to wet weight and return to µg/kg
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02655.001 | Area i |  | A | 15.7828 | 16.2048 | 30.173 | 97.06 | 119.848 | 148.544 | 108.032 | 110.986 | 109.72 | 117.738 | 120.692 | 96.638 | 62.034 | 139.26 | 25.9108 | 185.68 | 38.0644 | 116.05 | 65.41 | 42.1156 | 132.93 | 148.122
|  |  | MAR02655.002 | Area i |  | B | 12.3532 | 11.4632 | 25.5608 | 69.776 | 89 | 119.26 | 85.084 | 86.508 | 83.66 | 100.392 | 100.036 | 82.236 | 55.18 | 108.224 | 19.8292 | 144.18 | 31.2212 | 95.408 | 60.164 | 31.506 | 106.444 | 113.208
|  |  | MAR02655.003 | Area i |  | C | 13.7592 | 12.6672 | 26.4628 | 72.436 | 93.548 | 127.036 | 90.272 | 92.82 | 89.544 | 119.756 | 108.472 | 95.004 | 65.52 | 114.66 | 21.658 | 146.328 | 35.4536 | 100.464 | 64.428 | 32.9056 | 114.296 | 113.568
|  |  | MAR02655.004 | Area i |  | D | 15.6456 | 16.7056 | 32.86 | 99.216 | 121.264 | 153.064 | 108.12 | 112.36 | 111.088 | 115.328 | 111.936 | 92.856 | 61.48 | 142.464 | 26.2456 | 195.464 | 36.7184 | 121.264 | 69.536 | 42.2304 | 127.624 | 152.64
|  |  | MAR02655.005 | Area i |  | E | 12.5888 | 9.7216 | 24.6848 | 71.232 | 86.464 | 114.24 | 78.4 | 85.12 | 84.672 | 103.04 | 109.76 | 89.6 | 60.032 | 108.864 | 16.8 | 152.32 | 31.4048 | 81.984 | 60.928 | 31.8976 | 115.136 | 114.688
|  |  | MAR02655.006 | Area i |  | F | 13.8012 | 10.1184 | 25.296 | 72.54 | 90.396 | 123.132 | 84.444 | 89.28 | 85.56 | 108.624 | 109.74 | 93 | 69.192 | 113.088 | 18.5256 | 148.8 | 34.0008 | 91.884 | 59.52 | 31.7316 | 114.948 | 115.32
|  |  | MAR02655.007 | Area ii |  | G | 11.3373 | 8.8101 | 17.6553 | 55.458 | 71.253 | 99.684 | 70.551 | 72.657 | 68.445 | 98.28 | 89.154 | 84.591 | 58.266 | 89.856 | 15.9354 | 114.075 | 29.5191 | 77.22 | 50.895 | 25.5528 | 90.207 | 86.346
|  |  | MAR02655.008 | Area ii |  | H | 13.224 | 10.83 | 24.32 | 70.3 | 87.4 | 119.32 | 84.36 | 88.54 | 84.74 | 111.72 | 112.1 | 94.62 | 64.98 | 108.68 | 19.646 | 142.5 | 33.782 | 90.44 | 60.8 | 29.298 | 113.62 | 107.54
|  |  | MAR02655.009 | Area ii |  | I | 12.1 | 9.1476 | 23.5224 | 75.988 | 87.12 | 106.48 | 71.632 | 77.44 | 77.44 | 79.86 | 87.12 | 70.18 | 52.272 | 104.06 | 17.1336 | 151.008 | 26.136 | 78.408 | 44.044 | 29.3788 | 96.316 | 119.064
|  |  | MAR02655.010 | Area ii |  | J | 14.3808 | 12.8576 | 29.6576 | 96.768 | 107.968 | 133.504 | 88.256 | 96.768 | 97.216 | 99.456 | 99.008 | 85.12 | 62.272 | 129.472 | 22.0864 | 179.2 | 31.7184 | 98.112 | 56.448 | 35.1232 | 115.136 | 139.776
|  |  | MAR02655.011 | Area ii |  | K | 10.434 | 9.776 | 23.077 | 68.62 | 79.43 | 105.75 | 72.38 | 76.61 | 74.26 | 85.54 | 96.82 | 74.26 | 50.76 | 101.99 | 17.39 | 128.31 | 26.931 | 80.37 | 46.342 | 27.636 | 84.13 | 99.64
|  |  | MAR02655.012 | Area ii |  | L | 8.2839 | 6.9814 | 15.2132 | 45.4312 | 54.705 | 71.377 | 48.8177 | 51.8916 | 51.1622 | 60.436 | 58.352 | 51.2143 | 39.4918 | 64.604 | 11.5141 | 92.217 | 19.6938 | 53.663 | 35.3759 | 18.3913 | 63.562 | 72.94
|  |  | MAR02655.013 | Area iii |  | M | 3.6278 | 1.6986 | 6.1372 | 10.6248 | 11.6733 | 15.1683 | 9.3666 | 10.6248 | 11.1141 | 16.9158 | 13.2111 | 12.0927 | 7.8987 | 14.9586 | 2.4815 | 23.9058 | 6.1862 | 10.5549 | 12.4422 | 3.9773 | 17.3352 | 19.2924
|  |  | MAR02655.014 | Area iii |  | N | 3.7595 | 2.0249 | 6.8534 | 12.4608 | 13.806 | 17.9124 | 11.1864 | 12.3192 | 12.6732 | 22.0896 | 17.5584 | 15.222 | 10.6908 | 16.992 | 2.74 | 28.674 | 6.7331 | 12.4608 | 18.762 | 4.8144 | 20.178 | 23.1516
|  |  | MAR02655.015 | Area iii |  | O | 114.72 | 24.432 | 110.88 | 354.72 | 370.08 | 372 | 231.84 | 271.68 | 301.92 | 185.76 | 288.96 | 154.56 | 110.4 | 422.4 | 61.92 | 676.8 | 116.64 | 261.6 | 140.64 | 104.64 | 504 | 547.2
|  |  | MAR02655.016 | Area iii |  | P | 42.588 | 14.56 | 57.785 | 168.805 | 179.27 | 189.735 | 118.755 | 137.41 | 145.6 | 121.485 | 150.15 | 103.74 | 81.445 | 204.295 | 29.5295 | 334.425 | 48.23 | 132.86 | 91.455 | 54.6 | 228.865 | 277.095
[5 empty] | Averages: |  | 19.8991 | 11.1249 | 30.0087 | 90.0897 | 103.9516 | 126.0129 | 85.0935 | 92.0634 | 93.0509 | 96.6513 | 104.5668 | 80.9334 | 56.9946 | 123.9917 | 20.5841 | 177.7429 | 34.527 | 93.9214 | 58.5744 | 34.1124 | 127.7954 | 140.5994
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02655.001 | Area i |  | A | 15.7828 | 16.2048 | 30.173 | 97.06 | 119.848 | 148.544 | 108.032 | 110.986 | 109.72 | 117.738 | 120.692 | 96.638 | 62.034 | 139.26 | 25.9108 | 185.68 | 38.0644 | 116.05 | 65.41 | 42.1156 | 132.93 | 148.122
|  |  | MAR02655.002 | Area i |  | B | 12.3532 | 11.4632 | 25.5608 | 69.776 | 89 | 119.26 | 85.084 | 86.508 | 83.66 | 100.392 | 100.036 | 82.236 | 55.18 | 108.224 | 19.8292 | 144.18 | 31.2212 | 95.408 | 60.164 | 31.506 | 106.444 | 113.208
|  |  | MAR02655.003 | Area i |  | C | 13.7592 | 12.6672 | 26.4628 | 72.436 | 93.548 | 127.036 | 90.272 | 92.82 | 89.544 | 119.756 | 108.472 | 95.004 | 65.52 | 114.66 | 21.658 | 146.328 | 35.4536 | 100.464 | 64.428 | 32.9056 | 114.296 | 113.568
|  |  | MAR02655.004 | Area i |  | D | 15.6456 | 16.7056 | 32.86 | 99.216 | 121.264 | 153.064 | 108.12 | 112.36 | 111.088 | 115.328 | 111.936 | 92.856 | 61.48 | 142.464 | 26.2456 | 195.464 | 36.7184 | 121.264 | 69.536 | 42.2304 | 127.624 | 152.64
|  |  | MAR02655.005 | Area i |  | E | 12.5888 | 9.7216 | 24.6848 | 71.232 | 86.464 | 114.24 | 78.4 | 85.12 | 84.672 | 103.04 | 109.76 | 89.6 | 60.032 | 108.864 | 16.8 | 152.32 | 31.4048 | 81.984 | 60.928 | 31.8976 | 115.136 | 114.688
|  |  | MAR02655.006 | Area i |  | F | 13.8012 | 10.1184 | 25.296 | 72.54 | 90.396 | 123.132 | 84.444 | 89.28 | 85.56 | 108.624 | 109.74 | 93 | 69.192 | 113.088 | 18.5256 | 148.8 | 34.0008 | 91.884 | 59.52 | 31.7316 | 114.948 | 115.32
|  |  | MAR02655.007 | Area ii |  | G | 11.3373 | 8.8101 | 17.6553 | 55.458 | 71.253 | 99.684 | 70.551 | 72.657 | 68.445 | 98.28 | 89.154 | 84.591 | 58.266 | 89.856 | 15.9354 | 114.075 | 29.5191 | 77.22 | 50.895 | 25.5528 | 90.207 | 86.346
|  |  | MAR02655.008 | Area ii |  | H | 13.224 | 10.83 | 24.32 | 70.3 | 87.4 | 119.32 | 84.36 | 88.54 | 84.74 | 111.72 | 112.1 | 94.62 | 64.98 | 108.68 | 19.646 | 142.5 | 33.782 | 90.44 | 60.8 | 29.298 | 113.62 | 107.54
|  |  | MAR02655.009 | Area ii |  | I | 12.1 | 9.1476 | 23.5224 | 75.988 | 87.12 | 106.48 | 71.632 | 77.44 | 77.44 | 79.86 | 87.12 | 70.18 | 52.272 | 104.06 | 17.1336 | 151.008 | 26.136 | 78.408 | 44.044 | 29.3788 | 96.316 | 119.064
|  |  | MAR02655.010 | Area ii |  | J | 14.3808 | 12.8576 | 29.6576 | 96.768 | 107.968 | 133.504 | 88.256 | 96.768 | 97.216 | 99.456 | 99.008 | 85.12 | 62.272 | 129.472 | 22.0864 | 179.2 | 31.7184 | 98.112 | 56.448 | 35.1232 | 115.136 | 139.776
|  |  | MAR02655.011 | Area ii |  | K | 10.434 | 9.776 | 23.077 | 68.62 | 79.43 | 105.75 | 72.38 | 76.61 | 74.26 | 85.54 | 96.82 | 74.26 | 50.76 | 101.99 | 17.39 | 128.31 | 26.931 | 80.37 | 46.342 | 27.636 | 84.13 | 99.64
|  |  | MAR02655.012 | Area ii |  | L | 8.2839 | 6.9814 | 15.2132 | 45.4312 | 54.705 | 71.377 | 48.8177 | 51.8916 | 51.1622 | 60.436 | 58.352 | 51.2143 | 39.4918 | 64.604 | 11.5141 | 92.217 | 19.6938 | 53.663 | 35.3759 | 18.3913 | 63.562 | 72.94
|  |  | MAR02655.013 | Area iii |  | M | 3.6278 | 1.6986 | 6.1372 | 10.6248 | 11.6733 | 15.1683 | 9.3666 | 10.6248 | 11.1141 | 16.9158 | 13.2111 | 12.0927 | 7.8987 | 14.9586 | 2.4815 | 23.9058 | 6.1862 | 10.5549 | 12.4422 | 3.9773 | 17.3352 | 19.2924
|  |  | MAR02655.014 | Area iii |  | N | 3.7595 | 2.0249 | 6.8534 | 12.4608 | 13.806 | 17.9124 | 11.1864 | 12.3192 | 12.6732 | 22.0896 | 17.5584 | 15.222 | 10.6908 | 16.992 | 2.74 | 28.674 | 6.7331 | 12.4608 | 18.762 | 4.8144 | 20.178 | 23.1516
|  |  | MAR02655.015 | Area iii |  | O | 114.72 | 24.432 | 110.88 | 354.72 | 370.08 | 372 | 231.84 | 271.68 | 301.92 | 185.76 | 288.96 | 154.56 | 110.4 | 422.4 | 61.92 | 676.8 | 116.64 | 261.6 | 140.64 | 104.64 | 504 | 547.2
|  |  | MAR02655.016 | Area iii |  | P | 42.588 | 14.56 | 57.785 | 168.805 | 179.27 | 189.735 | 118.755 | 137.41 | 145.6 | 121.485 | 150.15 | 103.74 | 81.445 | 204.295 | 29.5295 | 334.425 | 48.23 | 132.86 | 91.455 | 54.6 | 228.865 | 277.095
[5 empty] | Averages: |  | 19.8991 | 11.1249 | 30.0087 | 90.0897 | 103.9516 | 126.0129 | 85.0935 | 92.0634 | 93.0509 | 96.6513 | 104.5668 | 80.9334 | 56.9946 | 123.9917 | 20.5841 | 177.7429 | 34.527 | 93.9214 | 58.5744 | 34.1124 | 127.7954 | 140.5994
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
|  |  | MAR02655.001 | Area i |  | A | 15.8 | 16.2 | 30.2 | 97.1 | 120 | 149 | 108 | 111 | 110 | 118 | 121 | 96.6 | 62 | 139 | 25.9 | 186 | 38.1 | 116 | 65.4 | 42.1 | 133 | 148
|  |  | MAR02655.002 | Area i |  | B | 12.4 | 11.5 | 25.6 | 69.8 | 89 | 119 | 85.1 | 86.5 | 83.7 | 100 | 100 | 82.2 | 55.2 | 108 | 19.8 | 144 | 31.2 | 95.4 | 60.2 | 31.5 | 106 | 113
|  |  | MAR02655.003 | Area i |  | C | 13.8 | 12.7 | 26.5 | 72.4 | 93.5 | 127 | 90.3 | 92.8 | 89.5 | 120 | 108 | 95 | 65.5 | 115 | 21.7 | 146 | 35.5 | 100 | 64.4 | 32.9 | 114 | 114
|  |  | MAR02655.004 | Area i |  | D | 15.6 | 16.7 | 32.9 | 99.2 | 121 | 153 | 108 | 112 | 111 | 115 | 112 | 92.9 | 61.5 | 142 | 26.2 | 195 | 36.7 | 121 | 69.5 | 42.2 | 128 | 153
|  |  | MAR02655.005 | Area i |  | E | 12.6 | 9.72 | 24.7 | 71.2 | 86.5 | 114 | 78.4 | 85.1 | 84.7 | 103 | 110 | 89.6 | 60 | 109 | 16.8 | 152 | 31.4 | 82 | 60.9 | 31.9 | 115 | 115
|  |  | MAR02655.006 | Area i |  | F | 13.8 | 10.1 | 25.3 | 72.5 | 90.4 | 123 | 84.4 | 89.3 | 85.6 | 109 | 110 | 93 | 69.2 | 113 | 18.5 | 149 | 34 | 91.9 | 59.5 | 31.7 | 115 | 115
|  |  | MAR02655.007 | Area ii |  | G | 11.3 | 8.81 | 17.7 | 55.5 | 71.3 | 99.7 | 70.6 | 72.7 | 68.4 | 98.3 | 89.2 | 84.6 | 58.3 | 89.9 | 15.9 | 114 | 29.5 | 77.2 | 50.9 | 25.6 | 90.2 | 86.3
|  |  | MAR02655.008 | Area ii |  | H | 13.2 | 10.8 | 24.3 | 70.3 | 87.4 | 119 | 84.4 | 88.5 | 84.7 | 112 | 112 | 94.6 | 65 | 109 | 19.6 | 143 | 33.8 | 90.4 | 60.8 | 29.3 | 114 | 108
|  |  | MAR02655.009 | Area ii |  | I | 12.1 | 9.15 | 23.5 | 76 | 87.1 | 106 | 71.6 | 77.4 | 77.4 | 79.9 | 87.1 | 70.2 | 52.3 | 104 | 17.1 | 151 | 26.1 | 78.4 | 44 | 29.4 | 96.3 | 119
|  |  | MAR02655.010 | Area ii |  | J | 14.4 | 12.9 | 29.7 | 96.8 | 108 | 134 | 88.3 | 96.8 | 97.2 | 99.5 | 99 | 85.1 | 62.3 | 129 | 22.1 | 179 | 31.7 | 98.1 | 56.4 | 35.1 | 115 | 140
|  |  | MAR02655.011 | Area ii |  | K | 10.4 | 9.78 | 23.1 | 68.6 | 79.4 | 106 | 72.4 | 76.6 | 74.3 | 85.5 | 96.8 | 74.3 | 50.8 | 102 | 17.4 | 128 | 26.9 | 80.4 | 46.3 | 27.6 | 84.1 | 99.6
|  |  | MAR02655.012 | Area ii |  | L | 8.28 | 6.98 | 15.2 | 45.4 | 54.7 | 71.4 | 48.8 | 51.9 | 51.2 | 60.4 | 58.4 | 51.2 | 39.5 | 64.6 | 11.5 | 92.2 | 19.7 | 53.7 | 35.4 | 18.4 | 63.6 | 72.9
|  |  | MAR02655.013 | Area iii |  | M | 3.63 | 1.7 | 6.14 | 10.6 | 11.7 | 15.2 | 9.37 | 10.6 | 11.1 | 16.9 | 13.2 | 12.1 | 7.9 | 15 | 2.48 | 23.9 | 6.19 | 10.6 | 12.4 | 3.98 | 17.3 | 19.3
|  |  | MAR02655.014 | Area iii |  | N | 3.76 | 2.02 | 6.85 | 12.5 | 13.8 | 17.9 | 11.2 | 12.3 | 12.7 | 22.1 | 17.6 | 15.2 | 10.7 | 17 | 2.74 | 28.7 | 6.73 | 12.5 | 18.8 | 4.81 | 20.2 | 23.2
|  |  | MAR02655.015 | Area iii |  | O | 115 | 24.4 | 111 | 355 | 370 | 372 | 232 | 272 | 302 | 186 | 289 | 155 | 110 | 422 | 61.9 | 677 | 117 | 262 | 141 | 105 | 504 | 547
|  |  | MAR02655.016 | Area iii |  | P | 42.6 | 14.6 | 57.8 | 169 | 179 | 190 | 119 | 137 | 146 | 121 | 150 | 104 | 81.4 | 204 | 29.5 | 334 | 48.2 | 133 | 91.5 | 54.6 | 229 | 277
[5 empty] | Averages: |  | 19.9169 | 11.1287 | 30.0306 | 90.1188 | 103.925 | 126.0125 | 85.1169 | 92.0312 | 93.0938 | 96.6625 | 104.5813 | 80.975 | 56.975 | 123.9062 | 20.57 | 177.675 | 34.545 | 93.9125 | 58.5875 | 34.1306 | 127.7937 | 140.6438
Average of dredge areas
[6 empty] | Dredge Area | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[6 empty] | Area i | 14 | 12.82 | 27.5333 | 80.3667 | 100.0667 | 130.8333 | 92.3667 | 96.1167 | 94.0833 | 110.8333 | 110.1667 | 91.55 | 62.2333 | 121 | 21.4833 | 162 | 34.4833 | 101.05 | 63.3167 | 35.3833 | 118.5 | 126.3333 | #DIV/0!
[6 empty] | Area ii | 11.6133 | 9.7367 | 22.25 | 68.7667 | 81.3167 | 106.0167 | 72.6833 | 77.3167 | 75.5333 | 89.2667 | 90.4167 | 76.6667 | 54.7 | 99.75 | 17.2667 | 134.5333 | 27.95 | 79.7 | 48.9667 | 27.5667 | 93.8667 | 104.3 | #DIV/0!
[6 empty] | Area iii | 41.2475 | 10.68 | 45.4475 | 136.775 | 143.625 | 148.775 | 92.8925 | 107.975 | 117.95 | 86.5 | 117.45 | 71.575 | 52.5 | 164.5 | 24.155 | 265.9 | 44.53 | 104.525 | 65.925 | 42.0975 | 192.625 | 216.625 | #DIV/0!
Area iv
Area v
Area vi
[6 empty] | Averages: | 22.2869 | 11.0789 | 31.7436 | 95.3028 | 108.3361 | 128.5417 | 85.9808 | 93.8028 | 95.8556 | 95.5333 | 106.0111 | 79.9306 | 56.4778 | 128.4167 | 20.9683 | 187.4778 | 35.6544 | 95.0917 | 59.4028 | 35.0158 | 134.9972 | 149.0861
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[6 empty] | Area i | 9.1 | 8.333 | 17.8967 | 52.2383 | 65.0433 | 85.0417 | 60.0383 | 62.4758 | 61.1542 | 72.0417 | 71.6083 | 59.5075 | 40.4517 | 78.65 | 13.9642 | 105.3 | 22.4142 | 65.6825 | 41.1558 | 22.9992 | 77.025 | 82.1167 | #DIV/0!
[6 empty] | Area ii | 3.484 | 2.921 | 6.675 | 20.63 | 24.395 | 31.805 | 21.805 | 23.195 | 22.66 | 26.78 | 27.125 | 23 | 16.41 | 29.925 | 5.18 | 40.36 | 8.385 | 23.91 | 14.69 | 8.27 | 28.16 | 31.29 | #DIV/0!
[6 empty] | Area iii | 2.0624 | 0.534 | 2.2724 | 6.8388 | 7.1813 | 7.4388 | 4.6446 | 5.3987 | 5.8975 | 4.325 | 5.8725 | 3.5788 | 2.625 | 8.225 | 1.2078 | 13.295 | 2.2265 | 5.2263 | 3.2963 | 2.1049 | 9.6313 | 10.8313 | #DIV/0!
Area iv
Area v
Area vi
PR average
[7 empty] | PAHs as µg/kg wet weight | [21 empty] | Total hydrocarbon content (mg/kg)
[7 empty] | Acenapthene | Acenapthylene | Anthracene | Benz[a]anthracene | Benzo[a]pyrene | Benzo[b]fluoranthene | Benzo[g,h,i]perylene | Benzo[e]pyrene | Benzo[k]fluoranthene | C1-Napthalenes | C1-Phenanthrenes | C2-Napthalenes | C3-Napthalenes | Chrysene | Dibenz[a,h]anthracene | Fluoranthene | Fluorene | Indeno[123-c,d]pyrene | Napthalene | Perylene | Phenanthrene | Pyrene
[7 empty] | 14.6464 | 11.788 | 26.844 | 79.7071 | 96.6196 | 124.2854 | 86.488 | 91.0696 | 89.7117 | 103.1467 | 104.6058 | 86.0863 | 59.4867 | 116.8 | 20.3519 | 158.955 | 33.0257 | 94.8187 | 59.1421 | 33.374 | 114.8162 | 124.2379

## PCB data
Polychlorinated biphenyl data
Determinand analysis outputs:
Instructions:
1. Record the laboratory/contractor responsible for PCB analysis |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | PCBs as mg/kg dry weight
2. Record the date the samples were analysed. | [5 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
3. Enter full dataset for each sample in the analysis results table | [5 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02655.001 | Area i | A | 0.00142 | 0.0007 | 0.00206 | 0.0017 | 0.00047 | 0.0025 | 0.00049 | 0.00168 | 0.0006 | 0.00288 | 0.00027 | 0.00031 | 0.00074 | 0.00123 | 0.00206 | 0.00038 | 0.00104 | 0.00054 | 0.00314 | 0.00226 | 0.0013 | 0.00049 | 0.00121 | 0.00152 | 0.00284
5. Enter methdological limit of detection for each PCB prior to inputting raw data |  |  | MAR02655.002 | Area i | B | 0.00119 | 0.00065 | 0.00203 | 0.0021 | 0.00053 | 0.0024 | 0.00039 | 0.00153 | 0.00045 | 0.00232 | 0.00023 | 0.0003 | 0.00079 | 0.00136 | 0.00172 | 0.00041 | 0.0011 | 0.00049 | 0.00337 | 0.00263 | 0.0013 | 0.00054 | 0.00114 | 0.00141 | 0.0028
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02655.003 | Area i | C | 0.00117 | 0.00069 | 0.00181 | 0.00162 | 0.00041 | 0.00207 | 0.00048 | 0.00134 | 0.00046 | 0.00237 | 0.00023 | 0.00031 | 0.00073 | 0.00141 | 0.00181 | 0.00035 | 0.00096 | 0.00043 | 0.00338 | 0.00249 | 0.00138 | 0.0005 | 0.00117 | 0.00143 | 0.00293
7. ICES 7 PCBs are highlighted in bold |  |  | MAR02655.004 | Area i | D | 0.00107 | 0.00053 | 0.00159 | 0.00167 | 0.00033 | 0.00172 | 0.00019 | 0.00122 | 0.00043 | 0.00224 | 0.00017 | 0.00034 | 0.00067 | 0.00118 | 0.00153 | 0.00032 | 0.00082 | 0.00041 | 0.00283 | 0.00217 | 0.00119 | 0.00047 | 0.00104 | 0.0012 | 0.00252
8. Where copying and pasting entries please use paste values only |  |  | MAR02655.005 | Area i | E | 0.00111 | 0.00062 | 0.00194 | 0.00158 | 0.00041 | 0.00209 | 0.00044 | 0.00136 | 0.00038 | 0.00226 | 0.00022 | 0.00026 | 0.0008 | 0.00118 | 0.0016 | 0.00034 | 0.00096 | 0.00038 | 0.00316 | 0.0023 | 0.00112 | 0.00049 | 0.00111 | 0.00125 | 0.0027
9. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.006 | Area i | F | 0.00135 | 0.00073 | 0.0021 | 0.00173 | 0.00042 | 0.00206 | 0.0003 | 0.00149 | 0.00039 | 0.00277 | 0.00024 | 0.00031 | 0.00076 | 0.00168 | 0.00174 | 0.0004 | 0.00098 | 0.0004 | 0.00354 | 0.00269 | 0.00134 | 0.00055 | 0.00136 | 0.00157 | 0.00304
| IDs should be separated by a comma |  | MAR02655.007 | Area ii | G | 0.00153 | 0.00072 | 0.00225 | 0.00206 | 0.00044 | 0.00212 | 0.00038 | 0.00168 | 0.00054 | 0.00265 | 0.00019 | 0.0004 | 0.00087 | 0.00183 | 0.00182 | 0.00033 | 0.00084 | 0.00051 | 0.00394 | 0.00296 | 0.00141 | 0.00069 | 0.00158 | 0.0018 | 0.00351
|  |  | MAR02655.008 | Area ii | H | 0.00129 | 0.00069 | 0.00213 | 0.00212 | 0.00046 | 0.00228 | 0.00042 | 0.00169 | 0.00045 | 0.00259 | 0.00023 | 0.00033 | 0.00081 | 0.00121 | 0.00173 | 0.0003 | 0.00081 | 0.00046 | 0.00367 | 0.00277 | 0.00143 | 0.00061 | 0.00135 | 0.00143 | 0.0033
Analysis information: |  |  | MAR02655.009 | Area ii | I | 0.00077 | 0.00047 | 0.00129 | 0.00142 | 0.00029 | 0.00125 | 0.00022 | 0.00098 | 0.00037 | 0.0016 | 0.00012 | 0.00025 | 0.00045 | 0.00076 | 0.001 | 0.00018 | 0.0005 | 0.00029 | 0.00219 | 0.00171 | 0.00085 | 0.00035 | 0.00079 | 0.00083 | 0.002
|  |  | MAR02655.010 | Area ii | J | 0.00086 | 0.00049 | 0.00139 | 0.00129 | 0.00032 | 0.00164 | 0.0003 | 0.00111 | 0.00037 | 0.00177 | 0.00015 | 0.00014 | 0.00051 | 0.00089 | 0.00122 | 0.00017 | 0.00063 | 0.0003 | 0.00232 | 0.00177 | 0.00092 | 0.00041 | 0.00087 | 0.00095 | 0.00217
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.011 | Area ii | K | 0.00161 | 0.00064 | 0.00205 | 0.00214 | 0.0005 | 0.00229 | 0.00035 | 0.00135 | 0.00038 | 0.00221 | 0.00027 | 0.00031 | 0.00057 | 0.00061 | 0.00126 | 0.00025 | 0.00071 | 0.00026 | 0.00189 | 0.0014 | 0.00083 | 0.00034 | 0.00076 | 0.0012 | 0.00182
| Date of analysis: | 2025-06-03 | MAR02655.012 | Area ii | L | 0.00063 | 0.00031 | 0.00092 | 0.00083 | 0.00018 | 0.00112 | 0.00016 | 0.00059 | 0.00017 | 0.00109 | <LOD | 0.00016 | 0.00032 | 0.00054 | 0.00072 | 0.00014 | 0.00047 | 0.00019 | 0.00155 | 0.00108 | 0.00056 | 0.00026 | 0.00058 | 0.00061 | 0.00151
|  |  | MAR02655.013 | Area iii | M | <LOD | <LOD | 0.0001 | 9e-05 | <LOD | 0.00012 | <LOD | 8e-05 | <LOD | 0.00014 | <LOD | <LOD | <LOD | <LOD | 0.0001 | <LOD | <LOD | <LOD | 0.00019 | 0.00012 | <LOD | <LOD | <LOD | <LOD | 0.00019
|  |  | MAR02655.014 | Area iii | N | <LOD | <LOD | 0.0001 | 9e-05 | <LOD | 0.00014 | <LOD | <LOD | <LOD | 0.00013 | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | 0.00021 | 0.00013 | 8e-05 | <LOD | 8e-05 | <LOD | 0.00019
|  |  | MAR02655.015 | Area iii | O | 0.00072 | 0.00034 | 0.00121 | 0.00118 | 0.00017 | 0.00107 | 0.0002 | 0.00086 | 0.0003 | 0.00129 | 0.0001 | 0.00018 | 0.00043 | 0.0007 | 0.00087 | 0.00017 | 0.00055 | 0.00021 | 0.00197 | 0.00145 | 0.00072 | 0.00031 | 0.00071 | 0.00077 | 0.00165
|  |  | MAR02655.016 | Area iii | P | 0.00083 | 0.00042 | 0.00126 | 0.00132 | 0.00029 | 0.00155 | 0.0004 | 0.00106 | 0.00032 | 0.00179 | 0.0002 | 0.00019 | 0.00051 | 0.0008 | 0.00123 | 0.00026 | 0.00067 | 0.00029 | 0.00216 | 0.00162 | 0.00082 | 0.00034 | 0.0008 | 0.00097 | 0.00189
|  |  | Limits of detection (mg/kg dry weight): |  |  | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05

## PCB calcs (hidden)
Polyaromatic hydrocarbon summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection:
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg dry weight | [24 empty] | ICES 7 | Total 25 congeners
| Application number: | SP2508 |  |  |  |  | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
| Application title: | DML1946v2 - Marine Application - Port Talbot |  |  |  |  | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
| Date sampled: | 2025-05-02 | MAR02655.001 | Area i |  | A | 0.00142 | 0.0007 | 0.00206 | 0.0017 | 0.00047 | 0.0025 | 0.00049 | 0.00168 | 0.0006 | 0.00288 | 0.00027 | 0.00031 | 0.00074 | 0.00123 | 0.00206 | 0.00038 | 0.00104 | 0.00054 | 0.00314 | 0.00226 | 0.0013 | 0.00049 | 0.00121 | 0.00152 | 0.00284 | 0.01522 | 0.03383
| Sampling location: | Port Talbot | MAR02655.002 | Area i |  | B | 0.00119 | 0.00065 | 0.00203 | 0.0021 | 0.00053 | 0.0024 | 0.00039 | 0.00153 | 0.00045 | 0.00232 | 0.00023 | 0.0003 | 0.00079 | 0.00136 | 0.00172 | 0.00041 | 0.0011 | 0.00049 | 0.00337 | 0.00263 | 0.0013 | 0.00054 | 0.00114 | 0.00141 | 0.0028 | 0.01451 | 0.03318
|  |  | MAR02655.003 | Area i |  | C | 0.00117 | 0.00069 | 0.00181 | 0.00162 | 0.00041 | 0.00207 | 0.00048 | 0.00134 | 0.00046 | 0.00237 | 0.00023 | 0.00031 | 0.00073 | 0.00141 | 0.00181 | 0.00035 | 0.00096 | 0.00043 | 0.00338 | 0.00249 | 0.00138 | 0.0005 | 0.00117 | 0.00143 | 0.00293 | 0.01385 | 0.03193
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.004 | Area i |  | D | 0.00107 | 0.00053 | 0.00159 | 0.00167 | 0.00033 | 0.00172 | 0.00019 | 0.00122 | 0.00043 | 0.00224 | 0.00017 | 0.00034 | 0.00067 | 0.00118 | 0.00153 | 0.00032 | 0.00082 | 0.00041 | 0.00283 | 0.00217 | 0.00119 | 0.00047 | 0.00104 | 0.0012 | 0.00252 | 0.01226 | 0.02785
| Date of analysis: | 2025-06-03 | MAR02655.005 | Area i |  | E | 0.00111 | 0.00062 | 0.00194 | 0.00158 | 0.00041 | 0.00209 | 0.00044 | 0.00136 | 0.00038 | 0.00226 | 0.00022 | 0.00026 | 0.0008 | 0.00118 | 0.0016 | 0.00034 | 0.00096 | 0.00038 | 0.00316 | 0.0023 | 0.00112 | 0.00049 | 0.00111 | 0.00125 | 0.0027 | 0.01305 | 0.03006
|  |  | MAR02655.006 | Area i |  | F | 0.00135 | 0.00073 | 0.0021 | 0.00173 | 0.00042 | 0.00206 | 0.0003 | 0.00149 | 0.00039 | 0.00277 | 0.00024 | 0.00031 | 0.00076 | 0.00168 | 0.00174 | 0.0004 | 0.00098 | 0.0004 | 0.00354 | 0.00269 | 0.00134 | 0.00055 | 0.00136 | 0.00157 | 0.00304 | 0.01476 | 0.03394
|  |  | MAR02655.007 | Area ii |  | G | 0.00153 | 0.00072 | 0.00225 | 0.00206 | 0.00044 | 0.00212 | 0.00038 | 0.00168 | 0.00054 | 0.00265 | 0.00019 | 0.0004 | 0.00087 | 0.00183 | 0.00182 | 0.00033 | 0.00084 | 0.00051 | 0.00394 | 0.00296 | 0.00141 | 0.00069 | 0.00158 | 0.0018 | 0.00351 | 0.01592 | 0.03705
|  |  | MAR02655.008 | Area ii |  | H | 0.00129 | 0.00069 | 0.00213 | 0.00212 | 0.00046 | 0.00228 | 0.00042 | 0.00169 | 0.00045 | 0.00259 | 0.00023 | 0.00033 | 0.00081 | 0.00121 | 0.00173 | 0.0003 | 0.00081 | 0.00046 | 0.00367 | 0.00277 | 0.00143 | 0.00061 | 0.00135 | 0.00143 | 0.0033 | 0.01511 | 0.03456
|  |  | MAR02655.009 | Area ii |  | I | 0.00077 | 0.00047 | 0.00129 | 0.00142 | 0.00029 | 0.00125 | 0.00022 | 0.00098 | 0.00037 | 0.0016 | 0.00012 | 0.00025 | 0.00045 | 0.00076 | 0.001 | 0.00018 | 0.0005 | 0.00029 | 0.00219 | 0.00171 | 0.00085 | 0.00035 | 0.00079 | 0.00083 | 0.002 | 0.00906 | 0.02093
|  |  | MAR02655.010 | Area ii |  | J | 0.00086 | 0.00049 | 0.00139 | 0.00129 | 0.00032 | 0.00164 | 0.0003 | 0.00111 | 0.00037 | 0.00177 | 0.00015 | 0.00014 | 0.00051 | 0.00089 | 0.00122 | 0.00017 | 0.00063 | 0.0003 | 0.00232 | 0.00177 | 0.00092 | 0.00041 | 0.00087 | 0.00095 | 0.00217 | 0.01005 | 0.02296
|  |  | MAR02655.011 | Area ii |  | K | 0.00161 | 0.00064 | 0.00205 | 0.00214 | 0.0005 | 0.00229 | 0.00035 | 0.00135 | 0.00038 | 0.00221 | 0.00027 | 0.00031 | 0.00057 | 0.00061 | 0.00126 | 0.00025 | 0.00071 | 0.00026 | 0.00189 | 0.0014 | 0.00083 | 0.00034 | 0.00076 | 0.0012 | 0.00182 | 0.0126 | 0.026
|  |  | MAR02655.012 | Area ii |  | L | 0.00063 | 0.00031 | 0.00092 | 0.00083 | 0.00018 | 0.00112 | 0.00016 | 0.00059 | 0.00017 | 0.00109 | 8e-05 | 0.00016 | 0.00032 | 0.00054 | 0.00072 | 0.00014 | 0.00047 | 0.00019 | 0.00155 | 0.00108 | 0.00056 | 0.00026 | 0.00058 | 0.00061 | 0.00151 | 0.00655 | 0.01477
|  |  | MAR02655.013 | Area iii |  | M | 8e-05 | 8e-05 | 0.0001 | 9e-05 | 8e-05 | 0.00012 | 8e-05 | 8e-05 | 8e-05 | 0.00014 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 0.0001 | 8e-05 | 8e-05 | 8e-05 | 0.00019 | 0.00012 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 0.00019 | 0.0008 | 0.00241
|  |  | MAR02655.014 | Area iii |  | N | 8e-05 | 8e-05 | 0.0001 | 9e-05 | 8e-05 | 0.00014 | 8e-05 | 8e-05 | 8e-05 | 0.00013 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 0.00021 | 0.00013 | 8e-05 | 8e-05 | 8e-05 | 8e-05 | 0.00019 | 0.00081 | 0.00243
|  |  | MAR02655.015 | Area iii |  | O | 0.00072 | 0.00034 | 0.00121 | 0.00118 | 0.00017 | 0.00107 | 0.0002 | 0.00086 | 0.0003 | 0.00129 | 0.0001 | 0.00018 | 0.00043 | 0.0007 | 0.00087 | 0.00017 | 0.00055 | 0.00021 | 0.00197 | 0.00145 | 0.00072 | 0.00031 | 0.00071 | 0.00077 | 0.00165 | 0.00787 | 0.01813
|  |  | MAR02655.016 | Area iii |  | P | 0.00083 | 0.00042 | 0.00126 | 0.00132 | 0.00029 | 0.00155 | 0.0004 | 0.00106 | 0.00032 | 0.00179 | 0.0002 | 0.00019 | 0.00051 | 0.0008 | 0.00123 | 0.00026 | 0.00067 | 0.00029 | 0.00216 | 0.00162 | 0.00082 | 0.00034 | 0.0008 | 0.00097 | 0.00189 | 0.00985 | 0.02199
[5 empty] | Averages: |  | 0.00098188 | 0.00051 | 0.0015144 | 0.0014338 | 0.00033625 | 0.0016513 | 0.000305 | 0.0011312 | 0.00036062 | 0.0018813 | 0.00017875 | 0.00024688 | 0.00057 | 0.00097125 | 0.0012806 | 0.00026 | 0.0007 | 0.0003325 | 0.0024694 | 0.0018469 | 0.00095813 | 0.00040688 | 0.00091438 | 0.0010687 | 0.0021913 | 0.010767 | 0.024501
[6 empty] | Action level 1: | [25 empty] | 0.01 | 0.02
[6 empty] | Action level 2: | [26 empty] | 0.2
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02655.001 | Area i |  | A | 0.00059924 | 0.0002954 | 0.00086932 | 0.0007174 | 0.00019834 | 0.001055 | 0.00020678 | 0.00070896 | 0.0002532 | 0.0012154 | 0.00011394 | 0.00013082 | 0.00031228 | 0.00051906 | 0.00086932 | 0.00016036 | 0.00043888 | 0.00022788 | 0.0013251 | 0.00095372 | 0.0005486 | 0.00020678 | 0.00051062 | 0.00064144 | 0.0011985 | 0.0064228 | 0.014276
|  |  | MAR02655.002 | Area i |  | B | 0.00042364 | 0.0002314 | 0.00072268 | 0.0007476 | 0.00018868 | 0.0008544 | 0.00013884 | 0.00054468 | 0.0001602 | 0.00082592 | 8.188e-05 | 0.0001068 | 0.00028124 | 0.00048416 | 0.00061232 | 0.00014596 | 0.0003916 | 0.00017444 | 0.0011997 | 0.00093628 | 0.0004628 | 0.00019224 | 0.00040584 | 0.00050196 | 0.0009968 | 0.0051656 | 0.011812
|  |  | MAR02655.003 | Area i |  | C | 0.00042588 | 0.00025116 | 0.00065884 | 0.00058968 | 0.00014924 | 0.00075348 | 0.00017472 | 0.00048776 | 0.00016744 | 0.00086268 | 8.372e-05 | 0.00011284 | 0.00026572 | 0.00051324 | 0.00065884 | 0.0001274 | 0.00034944 | 0.00015652 | 0.0012303 | 0.00090636 | 0.00050232 | 0.000182 | 0.00042588 | 0.00052052 | 0.0010665 | 0.0050414 | 0.011623
|  |  | MAR02655.004 | Area i |  | D | 0.00045368 | 0.00022472 | 0.00067416 | 0.00070808 | 0.00013992 | 0.00072928 | 8.056e-05 | 0.00051728 | 0.00018232 | 0.00094976 | 7.208e-05 | 0.00014416 | 0.00028408 | 0.00050032 | 0.00064872 | 0.00013568 | 0.00034768 | 0.00017384 | 0.0011999 | 0.00092008 | 0.00050456 | 0.00019928 | 0.00044096 | 0.0005088 | 0.0010685 | 0.0051982 | 0.011808
|  |  | MAR02655.005 | Area i |  | E | 0.00049728 | 0.00027776 | 0.00086912 | 0.00070784 | 0.00018368 | 0.00093632 | 0.00019712 | 0.00060928 | 0.00017024 | 0.0010125 | 9.856e-05 | 0.00011648 | 0.0003584 | 0.00052864 | 0.0007168 | 0.00015232 | 0.00043008 | 0.00017024 | 0.0014157 | 0.0010304 | 0.00050176 | 0.00021952 | 0.00049728 | 0.00056 | 0.0012096 | 0.0058464 | 0.013467
|  |  | MAR02655.006 | Area i |  | F | 0.0005022 | 0.00027156 | 0.0007812 | 0.00064356 | 0.00015624 | 0.00076632 | 0.0001116 | 0.00055428 | 0.00014508 | 0.0010304 | 8.928e-05 | 0.00011532 | 0.00028272 | 0.00062496 | 0.00064728 | 0.0001488 | 0.00036456 | 0.0001488 | 0.0013169 | 0.0010007 | 0.00049848 | 0.0002046 | 0.00050592 | 0.00058404 | 0.0011309 | 0.0054907 | 0.012626
|  |  | MAR02655.007 | Area ii |  | G | 0.00053703 | 0.00025272 | 0.00078975 | 0.00072306 | 0.00015444 | 0.00074412 | 0.00013338 | 0.00058968 | 0.00018954 | 0.00093015 | 6.669e-05 | 0.0001404 | 0.00030537 | 0.00064233 | 0.00063882 | 0.00011583 | 0.00029484 | 0.00017901 | 0.0013829 | 0.001039 | 0.00049491 | 0.00024219 | 0.00055458 | 0.0006318 | 0.001232 | 0.0055879 | 0.013005
|  |  | MAR02655.008 | Area ii |  | H | 0.0004902 | 0.0002622 | 0.0008094 | 0.0008056 | 0.0001748 | 0.0008664 | 0.0001596 | 0.0006422 | 0.000171 | 0.0009842 | 8.74e-05 | 0.0001254 | 0.0003078 | 0.0004598 | 0.0006574 | 0.000114 | 0.0003078 | 0.0001748 | 0.0013946 | 0.0010526 | 0.0005434 | 0.0002318 | 0.000513 | 0.0005434 | 0.001254 | 0.0057418 | 0.013133
|  |  | MAR02655.009 | Area ii |  | I | 0.00037268 | 0.00022748 | 0.00062436 | 0.00068728 | 0.00014036 | 0.000605 | 0.00010648 | 0.00047432 | 0.00017908 | 0.0007744 | 5.808e-05 | 0.000121 | 0.0002178 | 0.00036784 | 0.000484 | 8.712e-05 | 0.000242 | 0.00014036 | 0.00106 | 0.00082764 | 0.0004114 | 0.0001694 | 0.00038236 | 0.00040172 | 0.000968 | 0.004385 | 0.01013
|  |  | MAR02655.010 | Area ii |  | J | 0.00038528 | 0.00021952 | 0.00062272 | 0.00057792 | 0.00014336 | 0.00073472 | 0.0001344 | 0.00049728 | 0.00016576 | 0.00079296 | 6.72e-05 | 6.272e-05 | 0.00022848 | 0.00039872 | 0.00054656 | 7.616e-05 | 0.00028224 | 0.0001344 | 0.0010394 | 0.00079296 | 0.00041216 | 0.00018368 | 0.00038976 | 0.0004256 | 0.00097216 | 0.0045024 | 0.010286
|  |  | MAR02655.011 | Area ii |  | K | 0.0007567 | 0.0003008 | 0.0009635 | 0.0010058 | 0.000235 | 0.0010763 | 0.0001645 | 0.0006345 | 0.0001786 | 0.0010387 | 0.0001269 | 0.0001457 | 0.0002679 | 0.0002867 | 0.0005922 | 0.0001175 | 0.0003337 | 0.0001222 | 0.0008883 | 0.000658 | 0.0003901 | 0.0001598 | 0.0003572 | 0.000564 | 0.0008554 | 0.005922 | 0.01222
|  |  | MAR02655.012 | Area ii |  | L | 0.00032823 | 0.00016151 | 0.00047932 | 0.00043243 | 9.378e-05 | 0.00058352 | 8.336e-05 | 0.00030739 | 8.857e-05 | 0.00056789 | 4.168e-05 | 8.336e-05 | 0.00016672 | 0.00028134 | 0.00037512 | 7.294e-05 | 0.00024487 | 9.899e-05 | 0.00080755 | 0.00056268 | 0.00029176 | 0.00013546 | 0.00030218 | 0.00031781 | 0.00078671 | 0.0034126 | 0.0076952
|  |  | MAR02655.013 | Area iii |  | M | 5.592e-05 | 5.592e-05 | 6.99e-05 | 6.291e-05 | 5.592e-05 | 8.388e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 9.786e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 6.99e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 0.00013281 | 8.388e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 0.00013281 | 0.0005592 | 0.0016846
|  |  | MAR02655.014 | Area iii |  | N | 5.664e-05 | 5.664e-05 | 7.08e-05 | 6.372e-05 | 5.664e-05 | 9.912e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 9.204e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 0.00014868 | 9.204e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 0.00013452 | 0.00057348 | 0.0017204
|  |  | MAR02655.015 | Area iii |  | O | 0.0003456 | 0.0001632 | 0.0005808 | 0.0005664 | 8.16e-05 | 0.0005136 | 9.6e-05 | 0.0004128 | 0.000144 | 0.0006192 | 4.8e-05 | 8.64e-05 | 0.0002064 | 0.000336 | 0.0004176 | 8.16e-05 | 0.000264 | 0.0001008 | 0.0009456 | 0.000696 | 0.0003456 | 0.0001488 | 0.0003408 | 0.0003696 | 0.000792 | 0.0037776 | 0.0087024
|  |  | MAR02655.016 | Area iii |  | P | 0.00037765 | 0.0001911 | 0.0005733 | 0.0006006 | 0.00013195 | 0.00070525 | 0.000182 | 0.0004823 | 0.0001456 | 0.00081445 | 9.1e-05 | 8.645e-05 | 0.00023205 | 0.000364 | 0.00055965 | 0.0001183 | 0.00030485 | 0.00013195 | 0.0009828 | 0.0007371 | 0.0003731 | 0.0001547 | 0.000364 | 0.00044135 | 0.00085995 | 0.0044818 | 0.010005
[5 empty] | Averages: |  | 0.00041299 | 0.00021519 | 0.00063495 | 0.00060249 | 0.00014275 | 0.00069417 | 0.00013012 | 0.00047345 | 0.00015332 | 0.00078803 | 7.7436e-05 | 0.00010565 | 0.00023935 | 0.00040123 | 0.00053445 | 0.00011041 | 0.00029432 | 0.00014042 | 0.0010294 | 0.00076809 | 0.00039959 | 0.00017143 | 0.00038143 | 0.00044529 | 0.00091614 | 0.0045068 | 0.010262
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02655.001 | Area i |  | A | 0.00059924 | 0.0002954 | 0.00086932 | 0.0007174 | 0.00019834 | 0.001055 | 0.00020678 | 0.00070896 | 0.0002532 | 0.0012154 | 0.00011394 | 0.00013082 | 0.00031228 | 0.00051906 | 0.00086932 | 0.00016036 | 0.00043888 | 0.00022788 | 0.0013251 | 0.00095372 | 0.0005486 | 0.00020678 | 0.00051062 | 0.00064144 | 0.0011985 | 0.0064228 | 0.014276
|  |  | MAR02655.002 | Area i |  | B | 0.00042364 | 0.0002314 | 0.00072268 | 0.0007476 | 0.00018868 | 0.0008544 | 0.00013884 | 0.00054468 | 0.0001602 | 0.00082592 | 8.188e-05 | 0.0001068 | 0.00028124 | 0.00048416 | 0.00061232 | 0.00014596 | 0.0003916 | 0.00017444 | 0.0011997 | 0.00093628 | 0.0004628 | 0.00019224 | 0.00040584 | 0.00050196 | 0.0009968 | 0.0051656 | 0.011812
|  |  | MAR02655.003 | Area i |  | C | 0.00042588 | 0.00025116 | 0.00065884 | 0.00058968 | 0.00014924 | 0.00075348 | 0.00017472 | 0.00048776 | 0.00016744 | 0.00086268 | 8.372e-05 | 0.00011284 | 0.00026572 | 0.00051324 | 0.00065884 | 0.0001274 | 0.00034944 | 0.00015652 | 0.0012303 | 0.00090636 | 0.00050232 | 0.000182 | 0.00042588 | 0.00052052 | 0.0010665 | 0.0050414 | 0.011623
|  |  | MAR02655.004 | Area i |  | D | 0.00045368 | 0.00022472 | 0.00067416 | 0.00070808 | 0.00013992 | 0.00072928 | 8.056e-05 | 0.00051728 | 0.00018232 | 0.00094976 | 7.208e-05 | 0.00014416 | 0.00028408 | 0.00050032 | 0.00064872 | 0.00013568 | 0.00034768 | 0.00017384 | 0.0011999 | 0.00092008 | 0.00050456 | 0.00019928 | 0.00044096 | 0.0005088 | 0.0010685 | 0.0051982 | 0.011808
|  |  | MAR02655.005 | Area i |  | E | 0.00049728 | 0.00027776 | 0.00086912 | 0.00070784 | 0.00018368 | 0.00093632 | 0.00019712 | 0.00060928 | 0.00017024 | 0.0010125 | 9.856e-05 | 0.00011648 | 0.0003584 | 0.00052864 | 0.0007168 | 0.00015232 | 0.00043008 | 0.00017024 | 0.0014157 | 0.0010304 | 0.00050176 | 0.00021952 | 0.00049728 | 0.00056 | 0.0012096 | 0.0058464 | 0.013467
|  |  | MAR02655.006 | Area i |  | F | 0.0005022 | 0.00027156 | 0.0007812 | 0.00064356 | 0.00015624 | 0.00076632 | 0.0001116 | 0.00055428 | 0.00014508 | 0.0010304 | 8.928e-05 | 0.00011532 | 0.00028272 | 0.00062496 | 0.00064728 | 0.0001488 | 0.00036456 | 0.0001488 | 0.0013169 | 0.0010007 | 0.00049848 | 0.0002046 | 0.00050592 | 0.00058404 | 0.0011309 | 0.0054907 | 0.012626
|  |  | MAR02655.007 | Area ii |  | G | 0.00053703 | 0.00025272 | 0.00078975 | 0.00072306 | 0.00015444 | 0.00074412 | 0.00013338 | 0.00058968 | 0.00018954 | 0.00093015 | 6.669e-05 | 0.0001404 | 0.00030537 | 0.00064233 | 0.00063882 | 0.00011583 | 0.00029484 | 0.00017901 | 0.0013829 | 0.001039 | 0.00049491 | 0.00024219 | 0.00055458 | 0.0006318 | 0.001232 | 0.0055879 | 0.013005
|  |  | MAR02655.008 | Area ii |  | H | 0.0004902 | 0.0002622 | 0.0008094 | 0.0008056 | 0.0001748 | 0.0008664 | 0.0001596 | 0.0006422 | 0.000171 | 0.0009842 | 8.74e-05 | 0.0001254 | 0.0003078 | 0.0004598 | 0.0006574 | 0.000114 | 0.0003078 | 0.0001748 | 0.0013946 | 0.0010526 | 0.0005434 | 0.0002318 | 0.000513 | 0.0005434 | 0.001254 | 0.0057418 | 0.013133
|  |  | MAR02655.009 | Area ii |  | I | 0.00037268 | 0.00022748 | 0.00062436 | 0.00068728 | 0.00014036 | 0.000605 | 0.00010648 | 0.00047432 | 0.00017908 | 0.0007744 | 5.808e-05 | 0.000121 | 0.0002178 | 0.00036784 | 0.000484 | 8.712e-05 | 0.000242 | 0.00014036 | 0.00106 | 0.00082764 | 0.0004114 | 0.0001694 | 0.00038236 | 0.00040172 | 0.000968 | 0.004385 | 0.01013
|  |  | MAR02655.010 | Area ii |  | J | 0.00038528 | 0.00021952 | 0.00062272 | 0.00057792 | 0.00014336 | 0.00073472 | 0.0001344 | 0.00049728 | 0.00016576 | 0.00079296 | 6.72e-05 | 6.272e-05 | 0.00022848 | 0.00039872 | 0.00054656 | 7.616e-05 | 0.00028224 | 0.0001344 | 0.0010394 | 0.00079296 | 0.00041216 | 0.00018368 | 0.00038976 | 0.0004256 | 0.00097216 | 0.0045024 | 0.010286
|  |  | MAR02655.011 | Area ii |  | K | 0.0007567 | 0.0003008 | 0.0009635 | 0.0010058 | 0.000235 | 0.0010763 | 0.0001645 | 0.0006345 | 0.0001786 | 0.0010387 | 0.0001269 | 0.0001457 | 0.0002679 | 0.0002867 | 0.0005922 | 0.0001175 | 0.0003337 | 0.0001222 | 0.0008883 | 0.000658 | 0.0003901 | 0.0001598 | 0.0003572 | 0.000564 | 0.0008554 | 0.005922 | 0.01222
|  |  | MAR02655.012 | Area ii |  | L | 0.00032823 | 0.00016151 | 0.00047932 | 0.00043243 | 9.378e-05 | 0.00058352 | 8.336e-05 | 0.00030739 | 8.857e-05 | 0.00056789 | 4.168e-05 | 8.336e-05 | 0.00016672 | 0.00028134 | 0.00037512 | 7.294e-05 | 0.00024487 | 9.899e-05 | 0.00080755 | 0.00056268 | 0.00029176 | 0.00013546 | 0.00030218 | 0.00031781 | 0.00078671 | 0.0034126 | 0.0076952
|  |  | MAR02655.013 | Area iii |  | M | 5.592e-05 | 5.592e-05 | 6.99e-05 | 6.291e-05 | 5.592e-05 | 8.388e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 9.786e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 6.99e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 0.00013281 | 8.388e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 5.592e-05 | 0.00013281 | 0.0005592 | 0.0016846
|  |  | MAR02655.014 | Area iii |  | N | 5.664e-05 | 5.664e-05 | 7.08e-05 | 6.372e-05 | 5.664e-05 | 9.912e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 9.204e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 0.00014868 | 9.204e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 5.664e-05 | 0.00013452 | 0.00057348 | 0.0017204
|  |  | MAR02655.015 | Area iii |  | O | 0.0003456 | 0.0001632 | 0.0005808 | 0.0005664 | 8.16e-05 | 0.0005136 | 9.6e-05 | 0.0004128 | 0.000144 | 0.0006192 | 4.8e-05 | 8.64e-05 | 0.0002064 | 0.000336 | 0.0004176 | 8.16e-05 | 0.000264 | 0.0001008 | 0.0009456 | 0.000696 | 0.0003456 | 0.0001488 | 0.0003408 | 0.0003696 | 0.000792 | 0.0037776 | 0.0087024
|  |  | MAR02655.016 | Area iii |  | P | 0.00037765 | 0.0001911 | 0.0005733 | 0.0006006 | 0.00013195 | 0.00070525 | 0.000182 | 0.0004823 | 0.0001456 | 0.00081445 | 9.1e-05 | 8.645e-05 | 0.00023205 | 0.000364 | 0.00055965 | 0.0001183 | 0.00030485 | 0.00013195 | 0.0009828 | 0.0007371 | 0.0003731 | 0.0001547 | 0.000364 | 0.00044135 | 0.00085995 | 0.0044818 | 0.010005
[5 empty] | Averages: |  | 0.00041299 | 0.00021519 | 0.00063495 | 0.00060249 | 0.00014275 | 0.00069417 | 0.00013012 | 0.00047345 | 0.00015332 | 0.00078803 | 7.7436e-05 | 0.00010565 | 0.00023935 | 0.00040123 | 0.00053445 | 0.00011041 | 0.00029432 | 0.00014042 | 0.0010294 | 0.00076809 | 0.00039959 | 0.00017143 | 0.00038143 | 0.00044529 | 0.00091614 | 0.0045068 | 0.010262
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID(s) | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
|  |  | MAR02655.001 | Area i |  | A | 0.000599 | 0.000295 | 0.000869 | 0.000717 | 0.000198 | 0.00106 | 0.000207 | 0.000709 | 0.000253 | 0.00122 | 0.000114 | 0.000131 | 0.000312 | 0.000519 | 0.000869 | 0.00016 | 0.000439 | 0.000228 | 0.00133 | 0.000954 | 0.000549 | 0.000207 | 0.000511 | 0.000641 | 0.0012 | 0.00642 | 0.0143
|  |  | MAR02655.002 | Area i |  | B | 0.000424 | 0.000231 | 0.000723 | 0.000748 | 0.000189 | 0.000854 | 0.000139 | 0.000545 | 0.00016 | 0.000826 | 8.19e-05 | 0.000107 | 0.000281 | 0.000484 | 0.000612 | 0.000146 | 0.000392 | 0.000174 | 0.0012 | 0.000936 | 0.000463 | 0.000192 | 0.000406 | 0.000502 | 0.000997 | 0.00517 | 0.0118
|  |  | MAR02655.003 | Area i |  | C | 0.000426 | 0.000251 | 0.000659 | 0.00059 | 0.000149 | 0.000753 | 0.000175 | 0.000488 | 0.000167 | 0.000863 | 8.37e-05 | 0.000113 | 0.000266 | 0.000513 | 0.000659 | 0.000127 | 0.000349 | 0.000157 | 0.00123 | 0.000906 | 0.000502 | 0.000182 | 0.000426 | 0.000521 | 0.00107 | 0.00504 | 0.0116
|  |  | MAR02655.004 | Area i |  | D | 0.000454 | 0.000225 | 0.000674 | 0.000708 | 0.00014 | 0.000729 | 8.06e-05 | 0.000517 | 0.000182 | 0.00095 | 7.21e-05 | 0.000144 | 0.000284 | 0.0005 | 0.000649 | 0.000136 | 0.000348 | 0.000174 | 0.0012 | 0.00092 | 0.000505 | 0.000199 | 0.000441 | 0.000509 | 0.00107 | 0.0052 | 0.0118
|  |  | MAR02655.005 | Area i |  | E | 0.000497 | 0.000278 | 0.000869 | 0.000708 | 0.000184 | 0.000936 | 0.000197 | 0.000609 | 0.00017 | 0.00101 | 9.86e-05 | 0.000116 | 0.000358 | 0.000529 | 0.000717 | 0.000152 | 0.00043 | 0.00017 | 0.00142 | 0.00103 | 0.000502 | 0.00022 | 0.000497 | 0.00056 | 0.00121 | 0.00585 | 0.0135
|  |  | MAR02655.006 | Area i |  | F | 0.000502 | 0.000272 | 0.000781 | 0.000644 | 0.000156 | 0.000766 | 0.000112 | 0.000554 | 0.000145 | 0.00103 | 8.93e-05 | 0.000115 | 0.000283 | 0.000625 | 0.000647 | 0.000149 | 0.000365 | 0.000149 | 0.00132 | 0.001 | 0.000498 | 0.000205 | 0.000506 | 0.000584 | 0.00113 | 0.00549 | 0.0126
|  |  | MAR02655.007 | Area ii |  | G | 0.000537 | 0.000253 | 0.00079 | 0.000723 | 0.000154 | 0.000744 | 0.000133 | 0.00059 | 0.00019 | 0.00093 | 6.67e-05 | 0.00014 | 0.000305 | 0.000642 | 0.000639 | 0.000116 | 0.000295 | 0.000179 | 0.00138 | 0.00104 | 0.000495 | 0.000242 | 0.000555 | 0.000632 | 0.00123 | 0.00559 | 0.013
|  |  | MAR02655.008 | Area ii |  | H | 0.00049 | 0.000262 | 0.000809 | 0.000806 | 0.000175 | 0.000866 | 0.00016 | 0.000642 | 0.000171 | 0.000984 | 8.74e-05 | 0.000125 | 0.000308 | 0.00046 | 0.000657 | 0.000114 | 0.000308 | 0.000175 | 0.00139 | 0.00105 | 0.000543 | 0.000232 | 0.000513 | 0.000543 | 0.00125 | 0.00574 | 0.0131
|  |  | MAR02655.009 | Area ii |  | I | 0.000373 | 0.000227 | 0.000624 | 0.000687 | 0.00014 | 0.000605 | 0.000106 | 0.000474 | 0.000179 | 0.000774 | 5.81e-05 | 0.000121 | 0.000218 | 0.000368 | 0.000484 | 8.71e-05 | 0.000242 | 0.00014 | 0.00106 | 0.000828 | 0.000411 | 0.000169 | 0.000382 | 0.000402 | 0.000968 | 0.00439 | 0.0101
|  |  | MAR02655.010 | Area ii |  | J | 0.000385 | 0.00022 | 0.000623 | 0.000578 | 0.000143 | 0.000735 | 0.000134 | 0.000497 | 0.000166 | 0.000793 | 6.72e-05 | 6.27e-05 | 0.000228 | 0.000399 | 0.000547 | 7.62e-05 | 0.000282 | 0.000134 | 0.00104 | 0.000793 | 0.000412 | 0.000184 | 0.00039 | 0.000426 | 0.000972 | 0.0045 | 0.0103
|  |  | MAR02655.011 | Area ii |  | K | 0.000757 | 0.000301 | 0.000964 | 0.00101 | 0.000235 | 0.00108 | 0.000165 | 0.000635 | 0.000179 | 0.00104 | 0.000127 | 0.000146 | 0.000268 | 0.000287 | 0.000592 | 0.000118 | 0.000334 | 0.000122 | 0.000888 | 0.000658 | 0.00039 | 0.00016 | 0.000357 | 0.000564 | 0.000855 | 0.00592 | 0.0122
|  |  | MAR02655.012 | Area ii |  | L | 0.000328 | 0.000162 | 0.000479 | 0.000432 | 9.38e-05 | 0.000584 | 8.34e-05 | 0.000307 | 8.86e-05 | 0.000568 | 4.17e-05 | 8.34e-05 | 0.000167 | 0.000281 | 0.000375 | 7.29e-05 | 0.000245 | 9.9e-05 | 0.000808 | 0.000563 | 0.000292 | 0.000135 | 0.000302 | 0.000318 | 0.000787 | 0.00341 | 0.0077
|  |  | MAR02655.013 | Area iii |  | M | 5.59e-05 | 5.59e-05 | 6.99e-05 | 6.29e-05 | 5.59e-05 | 8.39e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 9.79e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 6.99e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 0.000133 | 8.39e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 5.59e-05 | 0.000133 | 0.000559 | 0.00168
|  |  | MAR02655.014 | Area iii |  | N | 5.66e-05 | 5.66e-05 | 7.08e-05 | 6.37e-05 | 5.66e-05 | 9.91e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 9.2e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 0.000149 | 9.2e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 5.66e-05 | 0.000135 | 0.000573 | 0.00172
|  |  | MAR02655.015 | Area iii |  | O | 0.000346 | 0.000163 | 0.000581 | 0.000566 | 8.16e-05 | 0.000514 | 9.6e-05 | 0.000413 | 0.000144 | 0.000619 | 4.8e-05 | 8.64e-05 | 0.000206 | 0.000336 | 0.000418 | 8.16e-05 | 0.000264 | 0.000101 | 0.000946 | 0.000696 | 0.000346 | 0.000149 | 0.000341 | 0.00037 | 0.000792 | 0.00378 | 0.0087
|  |  | MAR02655.016 | Area iii |  | P | 0.000378 | 0.000191 | 0.000573 | 0.000601 | 0.000132 | 0.000705 | 0.000182 | 0.000482 | 0.000146 | 0.000814 | 9.1e-05 | 8.65e-05 | 0.000232 | 0.000364 | 0.00056 | 0.000118 | 0.000305 | 0.000132 | 0.000983 | 0.000737 | 0.000373 | 0.000155 | 0.000364 | 0.000441 | 0.00086 | 0.00448 | 0.01
[5 empty] | Averages: |  | 0.00041303 | 0.00021522 | 0.00063492 | 0.00060279 | 0.00014268 | 0.00069462 | 0.00013016 | 0.00047341 | 0.00015332 | 0.00078818 | 7.745e-05 | 0.00010559 | 0.00023928 | 0.00040122 | 0.00053447 | 0.00011039 | 0.00029441 | 0.00014041 | 0.0010298 | 0.00076793 | 0.00039959 | 0.00017147 | 0.00038147 | 0.00044534 | 0.00091619 | 0.004507 | 0.010256
Average of dredge areas
[6 empty] | Dredge Area | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[6 empty] | Area i | 0.00048367 | 0.00025867 | 0.0007625 | 0.00068583 | 0.00016933 | 0.00084967 | 0.00015177 | 0.00057033 | 0.0001795 | 0.00098317 | 8.9933e-05 | 0.000121 | 0.00029733 | 0.00052833 | 0.00069217 | 0.000145 | 0.00038717 | 0.00017533 | 0.0012833 | 0.00095767 | 0.00050317 | 0.00020083 | 0.0004645 | 0.00055283 | 0.0011128 | 0.0055283 | 0.0126
[6 empty] | Area ii | 0.00047833 | 0.0002375 | 0.00071483 | 0.000706 | 0.0001568 | 0.000769 | 0.00013023 | 0.00052417 | 0.00016227 | 0.00084817 | 7.4683e-05 | 0.00011302 | 0.000249 | 0.00040617 | 0.000549 | 9.7367e-05 | 0.00028433 | 0.0001415 | 0.0010943 | 0.000822 | 0.00042383 | 0.000187 | 0.0004165 | 0.00048083 | 0.0010103 | 0.004925 | 0.011067
[6 empty] | Area iii | 0.00020913 | 0.00011663 | 0.00032368 | 0.0003234 | 8.1525e-05 | 0.0003505 | 9.7625e-05 | 0.00025188 | 0.00010062 | 0.00040573 | 6.2875e-05 | 7.135e-05 | 0.00013762 | 0.00020313 | 0.00027613 | 7.8025e-05 | 0.00017038 | 8.6375e-05 | 0.00055275 | 0.00040222 | 0.00020787 | 0.00010412 | 0.00020438 | 0.00023087 | 0.00048 | 0.002348 | 0.005525
Area iv
Area v
Area vi
[6 empty] | Averages: | 0.00039038 | 0.00020426 | 0.00060034 | 0.00057174 | 0.00013589 | 0.00065639 | 0.00012654 | 0.00044879 | 0.00014746 | 0.00074569 | 7.5831e-05 | 0.00010179 | 0.00022799 | 0.00037921 | 0.00050576 | 0.0001068 | 0.00028063 | 0.0001344 | 0.00097681 | 0.0007273 | 0.00037829 | 0.00016399 | 0.00036179 | 0.00042151 | 0.00086772 | 0.0042671 | 0.0097306
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[6 empty] | Area i | 0.00031438 | 0.00016813 | 0.00049563 | 0.00044579 | 0.00011007 | 0.00055228 | 9.8648e-05 | 0.00037072 | 0.00011668 | 0.00063906 | 5.8457e-05 | 7.865e-05 | 0.00019327 | 0.00034342 | 0.00044991 | 9.425e-05 | 0.00025166 | 0.00011397 | 0.00083417 | 0.00062248 | 0.00032706 | 0.00013054 | 0.00030193 | 0.00035934 | 0.00072334 | 0.0035934 | 0.00819
[6 empty] | Area ii | 0.0001435 | 7.125e-05 | 0.00021445 | 0.0002118 | 4.704e-05 | 0.0002307 | 3.907e-05 | 0.00015725 | 4.868e-05 | 0.00025445 | 2.2405e-05 | 3.3905e-05 | 7.47e-05 | 0.00012185 | 0.0001647 | 2.921e-05 | 8.53e-05 | 4.245e-05 | 0.0003283 | 0.0002466 | 0.00012715 | 5.61e-05 | 0.00012495 | 0.00014425 | 0.0003031 | 0.0014775 | 0.00332
[6 empty] | Area iii | 1.0456e-05 | 5.8313e-06 | 1.6184e-05 | 1.617e-05 | 4.0763e-06 | 1.7525e-05 | 4.8813e-06 | 1.2594e-05 | 5.0313e-06 | 2.0286e-05 | 3.1438e-06 | 3.5675e-06 | 6.8813e-06 | 1.0156e-05 | 1.3806e-05 | 3.9013e-06 | 8.5188e-06 | 4.3187e-06 | 2.7638e-05 | 2.0111e-05 | 1.0394e-05 | 5.2063e-06 | 1.0219e-05 | 1.1544e-05 | 2.4e-05 | 0.0001174 | 0.00027625
Area iv
Area v
Area vi
PR average
[7 empty] | PCBs as mg/kg wet weight | [24 empty] | ICES 7 | Total 25 congeners
[7 empty] | 2,2',4,5,5'-Pentachlorobiphenyl | 2,3,3',4,4'-Pentachlorobiphenyl | 2,3,3',4',6-Pentachlorobiphenyl | 2,3',4,4',5-Pentachlorobiphenyl | 2,2',3,3',4,4'-Hexachlorobiphenyl | 2,2',3,4,4',5'-Hexachlorobiphenyl | 2,2',3,4,5,5'-Hexachlorobiphenyl | 2,2',3,4',5',6-Hexachlorobiphenyl | 2,2',3,5,5',6-Hexachlorobiphenyl | 2,2',4,4',5,5'-Hexachlorobiphenyl | 2,3,3',4,4',5-Hexachlorobiphenyl | 2,3,3',4,4',6-Hexachlorobiphenyl | 2,2',3,3',4,4',5-Heptachlorobiphenyl | 2,2',5- Trichlorobiphenyl | 2,2',3,4,4',5,5'-Heptachlorobiphenyl | 2,2',3,4,4',5',6-Heptachlorobiphenyl | 2,2',3,4',5,5',6-Heptachlorobiphenyl | 2,2',3,3',4,4',5,5'-Octachlorobiphenyl | 2,4,4'-Trichlorobiphenyl | 2,4',5-Trichlorobiphenyl | 2,2',3,5'-Tetrachlorobiphenyl | 2,2',4,4'-Tetrachlorobiphenyl | 2,2',4,5'-Tetrachlorobiphenyl | 2,2',5,5'-Tetrachlorobiphenyl | 2,3',4,4'-Tetrachlorobiphenyl
[7 empty] | CB101 | CB105 | CB110 | CB118 | CB128 | CB138 | CB141 | CB149 | CB151 | CB153 | CB156 | CB158 | CB170 | CB18 | CB180 | CB183 | CB187 | CB194 | CB28 | CB31 | CB44 | CB47 | CB49 | CB52 | CB66
[7 empty] | 0.00046834 | 0.00024521 | 0.00072626 | 0.00067376 | 0.00016118 | 0.00080051 | 0.0001426 | 0.00054056 | 0.00017039 | 0.00091379 | 8.4005e-05 | 0.00011612 | 0.00027485 | 0.00047542 | 0.00062841 | 0.00012736 | 0.00034548 | 0.00016074 | 0.0011901 | 0.00088919 | 0.0004646 | 0.00019185 | 0.00043709 | 0.00051514 | 0.0010504 | 0.0051883 | 0.011786

## Organochlorine data
Organochlorine data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Organochlorine pesticides as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table | [5 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02655.001 | Area i | A | <LOD | <LOD | <LOD | 0.0001 | 0.0002 | 0.0002 | <LOD | 0.0007
5. Enter methdological limit of detection for each Organochlorine prior to inputting raw data |  |  | MAR02655.002 | Area i | B | <LOD | <LOD | <LOD | <LOD | 0.0003 | 0.0002 | 0.0002 | 0.0007
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02655.003 | Area i | C | <LOD | <LOD | <LOD | <LOD | 0.0003 | 0.0003 | <LOD | 0.0007
7. Where copying and pasting entries please use paste values only |  |  | MAR02655.004 | Area i | D | <LOD | <LOD | <LOD | <LOD | 0.0002 | 0.0002 | <LOD | 0.0007
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.005 | Area i | E | <LOD | <LOD | <LOD | 0.0001 | 0.0003 | 0.0002 | 0.0001 | 0.0008
| IDs should be separated by a comma |  | MAR02655.006 | Area i | F | <LOD | <LOD | <LOD | 0.0002 | 0.0003 | 0.0002 | <LOD | 0.0006
|  |  | MAR02655.007 | Area ii | G | <LOD | <LOD | <LOD | 0.0001 | 0.0002 | 0.0002 | <LOD | 0.0006
Analysis information: |  |  | MAR02655.008 | Area ii | H | <LOD | <LOD | <LOD | 0.0004 | 0.0003 | 0.0003 | <LOD | 0.0008
|  |  | MAR02655.009 | Area ii | I | <LOD | <LOD | <LOD | 0.0002 | 0.0002 | 0.0002 | <LOD | 0.0004
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.010 | Area ii | J | <LOD | <LOD | <LOD | <LOD | 0.0002 | 0.0002 | <LOD | 0.0005
| Date of analysis: | 2025-06-03 | MAR02655.011 | Area ii | K | <LOD | <LOD | <LOD | <LOD | 0.0002 | 0.0002 | <LOD | 0.0004
|  |  | MAR02655.012 | Area ii | L | <LOD | <LOD | <LOD | <LOD | 0.0001 | 0.0001 | <LOD | 0.0003
|  |  | MAR02655.013 | Area iii | M | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD
|  |  | MAR02655.014 | Area iii | N | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD
|  |  | MAR02655.015 | Area iii | O | <LOD | <LOD | <LOD | 0.0002 | 0.0003 | 0.0003 | 0.0138 | 0.0119
|  |  | MAR02655.016 | Area iii | P | <LOD | <LOD | <LOD | <LOD | 0.0002 | 0.0002 | 0.002 | 0.0026
|  |  | Limits of detection (mg/kg dry weight): |  |  | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001

## Organochlorine calcs (hidden)
Organochlorine summary information
Analysis information: |  |  | Determinand analysis outputs - adjusted for limits of detection
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg dry weight
| Application number: | SP2508 |  |  |  |  | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
| Application title: | DML1946v2 - Marine Application - Port Talbot | MAR02655.001 | Area i |  | A | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0001 | 0.0007
| Date sampled: | 2025-05-02 | MAR02655.002 | Area i |  | B | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0002 | 0.0002 | 0.0007
| Sampling location: | Port Talbot | MAR02655.003 | Area i |  | C | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0003 | 0.0001 | 0.0007
|  |  | MAR02655.004 | Area i |  | D | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0001 | 0.0007
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.005 | Area i |  | E | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003 | 0.0002 | 0.0001 | 0.0008
| Date of analysis: | 2025-06-03 | MAR02655.006 | Area i |  | F | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0003 | 0.0002 | 0.0001 | 0.0006
|  |  | MAR02655.007 | Area ii |  | G | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0001 | 0.0006
|  |  | MAR02655.008 | Area ii |  | H | 0.0001 | 0.0001 | 0.0001 | 0.0004 | 0.0003 | 0.0003 | 0.0001 | 0.0008
|  |  | MAR02655.009 | Area ii |  | I | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0002 | 0.0001 | 0.0004
|  |  | MAR02655.010 | Area ii |  | J | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0001 | 0.0005
|  |  | MAR02655.011 | Area ii |  | K | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.0001 | 0.0004
|  |  | MAR02655.012 | Area ii |  | L | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0003
|  |  | MAR02655.013 | Area iii |  | M | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001
|  |  | MAR02655.014 | Area iii |  | N | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001
|  |  | MAR02655.015 | Area iii |  | O | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0003 | 0.0003 | 0.0138 | 0.0119
|  |  | MAR02655.016 | Area iii |  | P | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0002 | 0.0002 | 0.002 | 0.0026
[5 empty] | Averages: |  | 0.0001 | 0.0001 | 0.0001 | 0.0001375 | 0.00021875 | 0.0002 | 0.0010813 | 0.0013688
[6 empty] | Action level 1: |  |  |  | 0.005 |  |  | 0.001
Transformation to wet weight (mg/kg)
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02655.001 | Area i |  | A | 4.22e-05 | 4.22e-05 | 4.22e-05 | 4.22e-05 | 8.44e-05 | 8.44e-05 | 4.22e-05 | 0.0002954
|  |  | MAR02655.002 | Area i |  | B | 3.56e-05 | 3.56e-05 | 3.56e-05 | 3.56e-05 | 0.0001068 | 7.12e-05 | 7.12e-05 | 0.0002492
|  |  | MAR02655.003 | Area i |  | C | 3.64e-05 | 3.64e-05 | 3.64e-05 | 3.64e-05 | 0.0001092 | 0.0001092 | 3.64e-05 | 0.0002548
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 4.24e-05 | 4.24e-05 | 4.24e-05 | 8.48e-05 | 8.48e-05 | 4.24e-05 | 0.0002968
|  |  | MAR02655.005 | Area i |  | E | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 0.0001344 | 8.96e-05 | 4.48e-05 | 0.0003584
|  |  | MAR02655.006 | Area i |  | F | 3.72e-05 | 3.72e-05 | 3.72e-05 | 7.44e-05 | 0.0001116 | 7.44e-05 | 3.72e-05 | 0.0002232
|  |  | MAR02655.007 | Area ii |  | G | 3.51e-05 | 3.51e-05 | 3.51e-05 | 3.51e-05 | 7.02e-05 | 7.02e-05 | 3.51e-05 | 0.0002106
|  |  | MAR02655.008 | Area ii |  | H | 3.8e-05 | 3.8e-05 | 3.8e-05 | 0.000152 | 0.000114 | 0.000114 | 3.8e-05 | 0.000304
|  |  | MAR02655.009 | Area ii |  | I | 4.84e-05 | 4.84e-05 | 4.84e-05 | 9.68e-05 | 9.68e-05 | 9.68e-05 | 4.84e-05 | 0.0001936
|  |  | MAR02655.010 | Area ii |  | J | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 8.96e-05 | 8.96e-05 | 4.48e-05 | 0.000224
|  |  | MAR02655.011 | Area ii |  | K | 4.7e-05 | 4.7e-05 | 4.7e-05 | 4.7e-05 | 9.4e-05 | 9.4e-05 | 4.7e-05 | 0.000188
|  |  | MAR02655.012 | Area ii |  | L | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 0.0001563
|  |  | MAR02655.013 | Area iii |  | M | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05
|  |  | MAR02655.014 | Area iii |  | N | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05
|  |  | MAR02655.015 | Area iii |  | O | 4.8e-05 | 4.8e-05 | 4.8e-05 | 9.6e-05 | 0.000144 | 0.000144 | 0.006624 | 0.005712
|  |  | MAR02655.016 | Area iii |  | P | 4.55e-05 | 4.55e-05 | 4.55e-05 | 4.55e-05 | 9.1e-05 | 9.1e-05 | 0.00091 | 0.001183
[5 empty] | Averages: |  | 4.6137e-05 | 4.6137e-05 | 4.6137e-05 | 6.1613e-05 | 9.5225e-05 | 8.7875e-05 | 0.00051339 | 0.00062437
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02655.001 | Area i |  | A | 4.22e-05 | 4.22e-05 | 4.22e-05 | 4.22e-05 | 8.44e-05 | 8.44e-05 | 4.22e-05 | 0.0002954
|  |  | MAR02655.002 | Area i |  | B | 3.56e-05 | 3.56e-05 | 3.56e-05 | 3.56e-05 | 0.0001068 | 7.12e-05 | 7.12e-05 | 0.0002492
|  |  | MAR02655.003 | Area i |  | C | 3.64e-05 | 3.64e-05 | 3.64e-05 | 3.64e-05 | 0.0001092 | 0.0001092 | 3.64e-05 | 0.0002548
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 4.24e-05 | 4.24e-05 | 4.24e-05 | 8.48e-05 | 8.48e-05 | 4.24e-05 | 0.0002968
|  |  | MAR02655.005 | Area i |  | E | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 0.0001344 | 8.96e-05 | 4.48e-05 | 0.0003584
|  |  | MAR02655.006 | Area i |  | F | 3.72e-05 | 3.72e-05 | 3.72e-05 | 7.44e-05 | 0.0001116 | 7.44e-05 | 3.72e-05 | 0.0002232
|  |  | MAR02655.007 | Area ii |  | G | 3.51e-05 | 3.51e-05 | 3.51e-05 | 3.51e-05 | 7.02e-05 | 7.02e-05 | 3.51e-05 | 0.0002106
|  |  | MAR02655.008 | Area ii |  | H | 3.8e-05 | 3.8e-05 | 3.8e-05 | 0.000152 | 0.000114 | 0.000114 | 3.8e-05 | 0.000304
|  |  | MAR02655.009 | Area ii |  | I | 4.84e-05 | 4.84e-05 | 4.84e-05 | 9.68e-05 | 9.68e-05 | 9.68e-05 | 4.84e-05 | 0.0001936
|  |  | MAR02655.010 | Area ii |  | J | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 8.96e-05 | 8.96e-05 | 4.48e-05 | 0.000224
|  |  | MAR02655.011 | Area ii |  | K | 4.7e-05 | 4.7e-05 | 4.7e-05 | 4.7e-05 | 9.4e-05 | 9.4e-05 | 4.7e-05 | 0.000188
|  |  | MAR02655.012 | Area ii |  | L | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 0.0001563
|  |  | MAR02655.013 | Area iii |  | M | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05
|  |  | MAR02655.014 | Area iii |  | N | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05
|  |  | MAR02655.015 | Area iii |  | O | 4.8e-05 | 4.8e-05 | 4.8e-05 | 9.6e-05 | 0.000144 | 0.000144 | 0.006624 | 0.005712
|  |  | MAR02655.016 | Area iii |  | P | 4.55e-05 | 4.55e-05 | 4.55e-05 | 4.55e-05 | 9.1e-05 | 9.1e-05 | 0.00091 | 0.001183
[5 empty] | Averages: |  | 4.6137e-05 | 4.6137e-05 | 4.6137e-05 | 6.1613e-05 | 9.5225e-05 | 8.7875e-05 | 0.00051339 | 0.00062437
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
|  |  | MAR02655.001 | Area i |  | A | 4.22e-05 | 4.22e-05 | 4.22e-05 | 4.22e-05 | 8.44e-05 | 8.44e-05 | 4.22e-05 | 0.000295
|  |  | MAR02655.002 | Area i |  | B | 3.56e-05 | 3.56e-05 | 3.56e-05 | 3.56e-05 | 0.000107 | 7.12e-05 | 7.12e-05 | 0.000249
|  |  | MAR02655.003 | Area i |  | C | 3.64e-05 | 3.64e-05 | 3.64e-05 | 3.64e-05 | 0.000109 | 0.000109 | 3.64e-05 | 0.000255
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 4.24e-05 | 4.24e-05 | 4.24e-05 | 8.48e-05 | 8.48e-05 | 4.24e-05 | 0.000297
|  |  | MAR02655.005 | Area i |  | E | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 0.000134 | 8.96e-05 | 4.48e-05 | 0.000358
|  |  | MAR02655.006 | Area i |  | F | 3.72e-05 | 3.72e-05 | 3.72e-05 | 7.44e-05 | 0.000112 | 7.44e-05 | 3.72e-05 | 0.000223
|  |  | MAR02655.007 | Area ii |  | G | 3.51e-05 | 3.51e-05 | 3.51e-05 | 3.51e-05 | 7.02e-05 | 7.02e-05 | 3.51e-05 | 0.000211
|  |  | MAR02655.008 | Area ii |  | H | 3.8e-05 | 3.8e-05 | 3.8e-05 | 0.000152 | 0.000114 | 0.000114 | 3.8e-05 | 0.000304
|  |  | MAR02655.009 | Area ii |  | I | 4.84e-05 | 4.84e-05 | 4.84e-05 | 9.68e-05 | 9.68e-05 | 9.68e-05 | 4.84e-05 | 0.000194
|  |  | MAR02655.010 | Area ii |  | J | 4.48e-05 | 4.48e-05 | 4.48e-05 | 4.48e-05 | 8.96e-05 | 8.96e-05 | 4.48e-05 | 0.000224
|  |  | MAR02655.011 | Area ii |  | K | 4.7e-05 | 4.7e-05 | 4.7e-05 | 4.7e-05 | 9.4e-05 | 9.4e-05 | 4.7e-05 | 0.000188
|  |  | MAR02655.012 | Area ii |  | L | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 5.21e-05 | 0.000156
|  |  | MAR02655.013 | Area iii |  | M | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05 | 6.99e-05
|  |  | MAR02655.014 | Area iii |  | N | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05 | 7.08e-05
|  |  | MAR02655.015 | Area iii |  | O | 4.8e-05 | 4.8e-05 | 4.8e-05 | 9.6e-05 | 0.000144 | 0.000144 | 0.00662 | 0.00571
|  |  | MAR02655.016 | Area iii |  | P | 4.55e-05 | 4.55e-05 | 4.55e-05 | 4.55e-05 | 9.1e-05 | 9.1e-05 | 0.00091 | 0.00118
[5 empty] | Averages: |  | 4.6137e-05 | 4.6137e-05 | 4.6137e-05 | 6.1613e-05 | 9.5225e-05 | 8.7862e-05 | 0.00051314 | 0.00062404
Average of dredge areas
[6 empty] | Dredge Area | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[6 empty] | Area i | 3.9767e-05 | 3.9767e-05 | 3.9767e-05 | 4.5967e-05 | 0.0001052 | 8.5567e-05 | 4.57e-05 | 0.0002795
[6 empty] | Area ii | 4.4233e-05 | 4.4233e-05 | 4.4233e-05 | 7.13e-05 | 8.6117e-05 | 8.6117e-05 | 4.4233e-05 | 0.00021283
[6 empty] | Area iii | 5.855e-05 | 5.855e-05 | 5.855e-05 | 7.055e-05 | 9.3925e-05 | 9.3925e-05 | 0.0019177 | 0.0017577
Area iv
Area v
Area vi
[6 empty] | Averages: | 4.7517e-05 | 4.7517e-05 | 4.7517e-05 | 6.2606e-05 | 9.5081e-05 | 8.8536e-05 | 0.0006692 | 0.00075
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[6 empty] | Area i | 2.5848e-05 | 2.5848e-05 | 2.5848e-05 | 2.9878e-05 | 6.838e-05 | 5.5618e-05 | 2.9705e-05 | 0.00018168
[6 empty] | Area ii | 1.327e-05 | 1.327e-05 | 1.327e-05 | 2.139e-05 | 2.5835e-05 | 2.5835e-05 | 1.327e-05 | 6.385e-05
[6 empty] | Area iii | 2.9275e-06 | 2.9275e-06 | 2.9275e-06 | 3.5275e-06 | 4.6963e-06 | 4.6963e-06 | 9.5884e-05 | 8.7884e-05
Area iv
Area v
Area vi
PR average
Organochlorines as mg/kg wet weight
[7 empty] | alpha-hexachlorocyclohexane (AHCH) | beta-hexachlorocyclohexane (BHCH) | gamma-hexachlorocyclohexane (GHCH) | Dieldrin | Hexachlorobenzene (HCB) | 1,1-Dichloro-2,2-bis(p-chlorophenyl) ethylene (PPDDE) | Dichlorodiphenyltrichloroethane (PPDDT) | 1,1-dichloro-2,2-bis(p-chlorophenyl)ethane (PPTDE)
[7 empty] | 4.2046e-05 | 4.2046e-05 | 4.2046e-05 | 5.4796e-05 | 9.8911e-05 | 8.615e-05 | 0.00013886 | 0.00033341

## BDE data
Brominated flame retardant data
Instructions: |  |  | Determinand analysis outputs:
1. Record the laboratory/contractor responsible for analysis
2. Record the date the samples were analysed. |  |  | Laboratory sample number | Dredge Area | Sample ID(s) | Brominated flame retardants as mg/kg dry weight
3. Enter full dataset for each sample in the analysis results table | [5 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
4. Analysis results should be reported in mg/kg (ppm) dry weight. |  |  | MAR02655.001 | Area i | A | <LOD | <LOD | 6e-05 | 5e-05 | <LOD | <LOD | 0.0185 | <LOD | 0.00022 | <LOD | <LOD | 0.00027
5. Enter methdological limit of detection for each BDE prior to inputting raw data |  |  | MAR02655.002 | Area i | B | 5e-05 | <LOD | 7e-05 | 6e-05 | <LOD | <LOD | 0.0288 | <LOD | 0.00024 | <LOD | <LOD | 0.00027
6. Where analysis outputs are less than the limits of detection please enter text "<LOD" |  |  | MAR02655.003 | Area i | C | 7e-05 | <LOD | 8e-05 | 6e-05 | <LOD | <LOD | 0.0271 | <LOD | 0.00024 | <LOD | <LOD | 0.00034
7. Where copying and pasting entries please use paste values only |  |  | MAR02655.004 | Area i | D | 0.0001 | <LOD | 8e-05 | 7e-05 | <LOD | 6e-05 | 0.0705 | <LOD | 0.00029 | <LOD | <LOD | 0.00067
8. Where entering multiple Sample IDs please use the pop-up form |  |  | MAR02655.005 | Area i | E | 7e-05 | <LOD | 0.00011 | 7e-05 | <LOD | 5e-05 | 0.024 | <LOD | 0.00028 | 6e-05 | <LOD | 0.00051
| IDs should be separated by a comma |  | MAR02655.006 | Area i | F | 5e-05 | <LOD | <LOD | 5e-05 | <LOD | <LOD | 0.022 | <LOD | 0.00023 | <LOD | <LOD | 0.00032
|  |  | MAR02655.007 | Area ii | G | 5e-05 | <LOD | 7e-05 | 6e-05 | <LOD | <LOD | 0.0193 | <LOD | 0.00022 | <LOD | <LOD | 0.00028
Analysis information: |  |  | MAR02655.008 | Area ii | H | 0.00012 | 0.00015 | 0.00019 | 0.00015 | 5e-05 | 0.00015 | 0.0201 | 7e-05 | 0.00027 | 9e-05 | 0.00011 | 0.00034
|  |  | MAR02655.009 | Area ii | I | <LOD | <LOD | 6e-05 | 6e-05 | <LOD | 7e-05 | 0.0228 | <LOD | 0.00018 | <LOD | <LOD | 0.00023
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.010 | Area ii | J | <LOD | <LOD | 7e-05 | 7e-05 | <LOD | 7e-05 | 0.0258 | <LOD | 0.00019 | 5e-05 | <LOD | 0.00021
| Date of analysis: | 2025-06-05 | MAR02655.011 | Area ii | K | <LOD | <LOD | 5e-05 | <LOD | <LOD | <LOD | 0.0201 | <LOD | 0.00014 | <LOD | <LOD | 0.00022
|  |  | MAR02655.012 | Area ii | L | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | 0.0172 | <LOD | 0.00014 | <LOD | <LOD | 0.00025
|  |  | MAR02655.013 | Area iii | M | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | 0.0055 | <LOD | <LOD | <LOD | <LOD | <LOD
|  |  | MAR02655.014 | Area iii | N | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | 0.0029 | <LOD | <LOD | <LOD | <LOD | <LOD
|  |  | MAR02655.015 | Area iii | O | <LOD | <LOD | <LOD | <LOD | <LOD | <LOD | 0.0163 | <LOD | 0.00015 | <LOD | <LOD | 0.00015
|  |  | MAR02655.016 | Area iii | P | 6e-05 | <LOD | 7e-05 | <LOD | <LOD | <LOD | 0.0173 | <LOD | 0.00026 | <LOD | <LOD | 0.00029
|  |  | Limits of detection (mg/kg dry weight): |  |  | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0001 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05

## BDE calcs (hidden)
Brominated flame retardant summary information
Analysis information: |  |  | determinand analysis outputs - adjusted for limits of detection
| Applicant: | Associated British Ports | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg dry weight
| Application number: | SP2508 |  |  |  |  | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
| Application title: | DML1946v2 - Marine Application - Port Talbot | MAR02655.001 | Area i |  | A | 5e-05 | 5e-05 | 6e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0185 | 5e-05 | 0.00022 | 5e-05 | 5e-05 | 0.00027
| Date sampled: | 2025-05-02 | MAR02655.002 | Area i |  | B | 5e-05 | 5e-05 | 7e-05 | 6e-05 | 5e-05 | 5e-05 | 0.0288 | 5e-05 | 0.00024 | 5e-05 | 5e-05 | 0.00027
| Sampling location: | Port Talbot | MAR02655.003 | Area i |  | C | 7e-05 | 5e-05 | 8e-05 | 6e-05 | 5e-05 | 5e-05 | 0.0271 | 5e-05 | 0.00024 | 5e-05 | 5e-05 | 0.00034
|  |  | MAR02655.004 | Area i |  | D | 0.0001 | 5e-05 | 8e-05 | 7e-05 | 5e-05 | 6e-05 | 0.0705 | 5e-05 | 0.00029 | 5e-05 | 5e-05 | 0.00067
| Laboratory/contractor: | SOCOTEC UK Ltd | MAR02655.005 | Area i |  | E | 7e-05 | 5e-05 | 0.00011 | 7e-05 | 5e-05 | 5e-05 | 0.024 | 5e-05 | 0.00028 | 6e-05 | 5e-05 | 0.00051
| Date of analysis: | 2025-06-05 | MAR02655.006 | Area i |  | F | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.022 | 5e-05 | 0.00023 | 5e-05 | 5e-05 | 0.00032
|  |  | MAR02655.007 | Area ii |  | G | 5e-05 | 5e-05 | 7e-05 | 6e-05 | 5e-05 | 5e-05 | 0.0193 | 5e-05 | 0.00022 | 5e-05 | 5e-05 | 0.00028
|  |  | MAR02655.008 | Area ii |  | H | 0.00012 | 0.00015 | 0.00019 | 0.00015 | 5e-05 | 0.00015 | 0.0201 | 7e-05 | 0.00027 | 9e-05 | 0.00011 | 0.00034
|  |  | MAR02655.009 | Area ii |  | I | 5e-05 | 5e-05 | 6e-05 | 6e-05 | 5e-05 | 7e-05 | 0.0228 | 5e-05 | 0.00018 | 5e-05 | 5e-05 | 0.00023
|  |  | MAR02655.010 | Area ii |  | J | 5e-05 | 5e-05 | 7e-05 | 7e-05 | 5e-05 | 7e-05 | 0.0258 | 5e-05 | 0.00019 | 5e-05 | 5e-05 | 0.00021
|  |  | MAR02655.011 | Area ii |  | K | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0201 | 5e-05 | 0.00014 | 5e-05 | 5e-05 | 0.00022
|  |  | MAR02655.012 | Area ii |  | L | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0172 | 5e-05 | 0.00014 | 5e-05 | 5e-05 | 0.00025
|  |  | MAR02655.013 | Area iii |  | M | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0055 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05
|  |  | MAR02655.014 | Area iii |  | N | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0029 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05
|  |  | MAR02655.015 | Area iii |  | O | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0163 | 5e-05 | 0.00015 | 5e-05 | 5e-05 | 0.00015
|  |  | MAR02655.016 | Area iii |  | P | 6e-05 | 5e-05 | 7e-05 | 5e-05 | 5e-05 | 5e-05 | 0.0173 | 5e-05 | 0.00026 | 5e-05 | 5e-05 | 0.00029
[5 empty] | Averages: |  | 6.0625e-05 | 5.625e-05 | 7.25e-05 | 6.25e-05 | 5e-05 | 5.9375e-05 | 0.022387 | 5.125e-05 | 0.00019687 | 5.3125e-05 | 5.375e-05 | 0.00027812
Transformation to wet weight
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02655.001 | Area i |  | A | 2.11e-05 | 2.11e-05 | 2.532e-05 | 2.11e-05 | 2.11e-05 | 2.11e-05 | 0.007807 | 2.11e-05 | 9.284e-05 | 2.11e-05 | 2.11e-05 | 0.00011394
|  |  | MAR02655.002 | Area i |  | B | 1.78e-05 | 1.78e-05 | 2.492e-05 | 2.136e-05 | 1.78e-05 | 1.78e-05 | 0.010253 | 1.78e-05 | 8.544e-05 | 1.78e-05 | 1.78e-05 | 9.612e-05
|  |  | MAR02655.003 | Area i |  | C | 2.548e-05 | 1.82e-05 | 2.912e-05 | 2.184e-05 | 1.82e-05 | 1.82e-05 | 0.0098644 | 1.82e-05 | 8.736e-05 | 1.82e-05 | 1.82e-05 | 0.00012376
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 2.12e-05 | 3.392e-05 | 2.968e-05 | 2.12e-05 | 2.544e-05 | 0.029892 | 2.12e-05 | 0.00012296 | 2.12e-05 | 2.12e-05 | 0.00028408
|  |  | MAR02655.005 | Area i |  | E | 3.136e-05 | 2.24e-05 | 4.928e-05 | 3.136e-05 | 2.24e-05 | 2.24e-05 | 0.010752 | 2.24e-05 | 0.00012544 | 2.688e-05 | 2.24e-05 | 0.00022848
|  |  | MAR02655.006 | Area i |  | F | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 0.008184 | 1.86e-05 | 8.556e-05 | 1.86e-05 | 1.86e-05 | 0.00011904
|  |  | MAR02655.007 | Area ii |  | G | 1.755e-05 | 1.755e-05 | 2.457e-05 | 2.106e-05 | 1.755e-05 | 1.755e-05 | 0.0067743 | 1.755e-05 | 7.722e-05 | 1.755e-05 | 1.755e-05 | 9.828e-05
|  |  | MAR02655.008 | Area ii |  | H | 4.56e-05 | 5.7e-05 | 7.22e-05 | 5.7e-05 | 1.9e-05 | 5.7e-05 | 0.007638 | 2.66e-05 | 0.0001026 | 3.42e-05 | 4.18e-05 | 0.0001292
|  |  | MAR02655.009 | Area ii |  | I | 2.42e-05 | 2.42e-05 | 2.904e-05 | 2.904e-05 | 2.42e-05 | 3.388e-05 | 0.011035 | 2.42e-05 | 8.712e-05 | 2.42e-05 | 2.42e-05 | 0.00011132
|  |  | MAR02655.010 | Area ii |  | J | 2.24e-05 | 2.24e-05 | 3.136e-05 | 3.136e-05 | 2.24e-05 | 3.136e-05 | 0.011558 | 2.24e-05 | 8.512e-05 | 2.24e-05 | 2.24e-05 | 9.408e-05
|  |  | MAR02655.011 | Area ii |  | K | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 0.009447 | 2.35e-05 | 6.58e-05 | 2.35e-05 | 2.35e-05 | 0.0001034
|  |  | MAR02655.012 | Area ii |  | L | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 0.0089612 | 2.605e-05 | 7.294e-05 | 2.605e-05 | 2.605e-05 | 0.00013025
|  |  | MAR02655.013 | Area iii |  | M | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 0.0038445 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05
|  |  | MAR02655.014 | Area iii |  | N | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 0.0020532 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05
|  |  | MAR02655.015 | Area iii |  | O | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 0.007824 | 2.4e-05 | 7.2e-05 | 2.4e-05 | 2.4e-05 | 7.2e-05
|  |  | MAR02655.016 | Area iii |  | P | 2.73e-05 | 2.275e-05 | 3.185e-05 | 2.275e-05 | 2.275e-05 | 2.275e-05 | 0.0078715 | 2.275e-05 | 0.0001183 | 2.275e-05 | 2.275e-05 | 0.00013195
[5 empty] | Averages: |  | 2.7356e-05 | 2.5444e-05 | 3.213e-05 | 2.8066e-05 | 2.3069e-05 | 2.6874e-05 | 0.00961 | 2.3544e-05 | 8.4441e-05 | 2.4299e-05 | 2.4494e-05 | 0.00011914
Removal of excluded areas
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02655.001 | Area i |  | A | 2.11e-05 | 2.11e-05 | 2.532e-05 | 2.11e-05 | 2.11e-05 | 2.11e-05 | 0.007807 | 2.11e-05 | 9.284e-05 | 2.11e-05 | 2.11e-05 | 0.00011394
|  |  | MAR02655.002 | Area i |  | B | 1.78e-05 | 1.78e-05 | 2.492e-05 | 2.136e-05 | 1.78e-05 | 1.78e-05 | 0.010253 | 1.78e-05 | 8.544e-05 | 1.78e-05 | 1.78e-05 | 9.612e-05
|  |  | MAR02655.003 | Area i |  | C | 2.548e-05 | 1.82e-05 | 2.912e-05 | 2.184e-05 | 1.82e-05 | 1.82e-05 | 0.0098644 | 1.82e-05 | 8.736e-05 | 1.82e-05 | 1.82e-05 | 0.00012376
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 2.12e-05 | 3.392e-05 | 2.968e-05 | 2.12e-05 | 2.544e-05 | 0.029892 | 2.12e-05 | 0.00012296 | 2.12e-05 | 2.12e-05 | 0.00028408
|  |  | MAR02655.005 | Area i |  | E | 3.136e-05 | 2.24e-05 | 4.928e-05 | 3.136e-05 | 2.24e-05 | 2.24e-05 | 0.010752 | 2.24e-05 | 0.00012544 | 2.688e-05 | 2.24e-05 | 0.00022848
|  |  | MAR02655.006 | Area i |  | F | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 0.008184 | 1.86e-05 | 8.556e-05 | 1.86e-05 | 1.86e-05 | 0.00011904
|  |  | MAR02655.007 | Area ii |  | G | 1.755e-05 | 1.755e-05 | 2.457e-05 | 2.106e-05 | 1.755e-05 | 1.755e-05 | 0.0067743 | 1.755e-05 | 7.722e-05 | 1.755e-05 | 1.755e-05 | 9.828e-05
|  |  | MAR02655.008 | Area ii |  | H | 4.56e-05 | 5.7e-05 | 7.22e-05 | 5.7e-05 | 1.9e-05 | 5.7e-05 | 0.007638 | 2.66e-05 | 0.0001026 | 3.42e-05 | 4.18e-05 | 0.0001292
|  |  | MAR02655.009 | Area ii |  | I | 2.42e-05 | 2.42e-05 | 2.904e-05 | 2.904e-05 | 2.42e-05 | 3.388e-05 | 0.011035 | 2.42e-05 | 8.712e-05 | 2.42e-05 | 2.42e-05 | 0.00011132
|  |  | MAR02655.010 | Area ii |  | J | 2.24e-05 | 2.24e-05 | 3.136e-05 | 3.136e-05 | 2.24e-05 | 3.136e-05 | 0.011558 | 2.24e-05 | 8.512e-05 | 2.24e-05 | 2.24e-05 | 9.408e-05
|  |  | MAR02655.011 | Area ii |  | K | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 0.009447 | 2.35e-05 | 6.58e-05 | 2.35e-05 | 2.35e-05 | 0.0001034
|  |  | MAR02655.012 | Area ii |  | L | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 2.605e-05 | 0.0089612 | 2.605e-05 | 7.294e-05 | 2.605e-05 | 2.605e-05 | 0.00013025
|  |  | MAR02655.013 | Area iii |  | M | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 0.0038445 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05 | 3.495e-05
|  |  | MAR02655.014 | Area iii |  | N | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 0.0020532 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05
|  |  | MAR02655.015 | Area iii |  | O | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 0.007824 | 2.4e-05 | 7.2e-05 | 2.4e-05 | 2.4e-05 | 7.2e-05
|  |  | MAR02655.016 | Area iii |  | P | 2.73e-05 | 2.275e-05 | 3.185e-05 | 2.275e-05 | 2.275e-05 | 2.275e-05 | 0.0078715 | 2.275e-05 | 0.0001183 | 2.275e-05 | 2.275e-05 | 0.00013195
[5 empty] | Averages: |  | 2.7356e-05 | 2.5444e-05 | 3.213e-05 | 2.8066e-05 | 2.3069e-05 | 2.6874e-05 | 0.00961 | 2.3544e-05 | 8.4441e-05 | 2.4299e-05 | 2.4494e-05 | 0.00011914
Force significant figures
|  |  | Laboratory sample number | Dredge Area | Excluded (y if yes) | Sample ID | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
|  |  | MAR02655.001 | Area i |  | A | 2.11e-05 | 2.11e-05 | 2.53e-05 | 2.11e-05 | 2.11e-05 | 2.11e-05 | 0.00781 | 2.11e-05 | 9.28e-05 | 2.11e-05 | 2.11e-05 | 0.000114
|  |  | MAR02655.002 | Area i |  | B | 1.78e-05 | 1.78e-05 | 2.49e-05 | 2.14e-05 | 1.78e-05 | 1.78e-05 | 0.0103 | 1.78e-05 | 8.54e-05 | 1.78e-05 | 1.78e-05 | 9.61e-05
|  |  | MAR02655.003 | Area i |  | C | 2.55e-05 | 1.82e-05 | 2.91e-05 | 2.18e-05 | 1.82e-05 | 1.82e-05 | 0.00986 | 1.82e-05 | 8.74e-05 | 1.82e-05 | 1.82e-05 | 0.000124
|  |  | MAR02655.004 | Area i |  | D | 4.24e-05 | 2.12e-05 | 3.39e-05 | 2.97e-05 | 2.12e-05 | 2.54e-05 | 0.0299 | 2.12e-05 | 0.000123 | 2.12e-05 | 2.12e-05 | 0.000284
|  |  | MAR02655.005 | Area i |  | E | 3.14e-05 | 2.24e-05 | 4.93e-05 | 3.14e-05 | 2.24e-05 | 2.24e-05 | 0.0108 | 2.24e-05 | 0.000125 | 2.69e-05 | 2.24e-05 | 0.000228
|  |  | MAR02655.006 | Area i |  | F | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 1.86e-05 | 0.00818 | 1.86e-05 | 8.56e-05 | 1.86e-05 | 1.86e-05 | 0.000119
|  |  | MAR02655.007 | Area ii |  | G | 1.76e-05 | 1.76e-05 | 2.46e-05 | 2.11e-05 | 1.76e-05 | 1.76e-05 | 0.00677 | 1.76e-05 | 7.72e-05 | 1.76e-05 | 1.76e-05 | 9.83e-05
|  |  | MAR02655.008 | Area ii |  | H | 4.56e-05 | 5.7e-05 | 7.22e-05 | 5.7e-05 | 1.9e-05 | 5.7e-05 | 0.00764 | 2.66e-05 | 0.000103 | 3.42e-05 | 4.18e-05 | 0.000129
|  |  | MAR02655.009 | Area ii |  | I | 2.42e-05 | 2.42e-05 | 2.9e-05 | 2.9e-05 | 2.42e-05 | 3.39e-05 | 0.011 | 2.42e-05 | 8.71e-05 | 2.42e-05 | 2.42e-05 | 0.000111
|  |  | MAR02655.010 | Area ii |  | J | 2.24e-05 | 2.24e-05 | 3.14e-05 | 3.14e-05 | 2.24e-05 | 3.14e-05 | 0.0116 | 2.24e-05 | 8.51e-05 | 2.24e-05 | 2.24e-05 | 9.41e-05
|  |  | MAR02655.011 | Area ii |  | K | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 2.35e-05 | 0.00945 | 2.35e-05 | 6.58e-05 | 2.35e-05 | 2.35e-05 | 0.000103
|  |  | MAR02655.012 | Area ii |  | L | 2.61e-05 | 2.61e-05 | 2.61e-05 | 2.61e-05 | 2.61e-05 | 2.61e-05 | 0.00896 | 2.61e-05 | 7.29e-05 | 2.61e-05 | 2.61e-05 | 0.00013
|  |  | MAR02655.013 | Area iii |  | M | 3.5e-05 | 3.5e-05 | 3.5e-05 | 3.5e-05 | 3.5e-05 | 3.5e-05 | 0.00384 | 3.5e-05 | 3.5e-05 | 3.5e-05 | 3.5e-05 | 3.5e-05
|  |  | MAR02655.014 | Area iii |  | N | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 0.00205 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05 | 3.54e-05
|  |  | MAR02655.015 | Area iii |  | O | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 2.4e-05 | 0.00782 | 2.4e-05 | 7.2e-05 | 2.4e-05 | 2.4e-05 | 7.2e-05
|  |  | MAR02655.016 | Area iii |  | P | 2.73e-05 | 2.28e-05 | 3.19e-05 | 2.28e-05 | 2.28e-05 | 2.28e-05 | 0.00787 | 2.28e-05 | 0.000118 | 2.28e-05 | 2.28e-05 | 0.000132
[5 empty] | Averages: |  | 2.7369e-05 | 2.5456e-05 | 3.2137e-05 | 2.8081e-05 | 2.3081e-05 | 2.6887e-05 | 0.0096156 | 2.3556e-05 | 8.4419e-05 | 2.4312e-05 | 2.4506e-05 | 0.00011906
Average of dredge areas
[6 empty] | Dredge Area | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[6 empty] | Area i | 2.6133e-05 | 1.9883e-05 | 3.0183e-05 | 2.4e-05 | 1.9883e-05 | 2.0583e-05 | 0.012808 | 1.9883e-05 | 9.9867e-05 | 2.0633e-05 | 1.9883e-05 | 0.00016085
[6 empty] | Area ii | 2.6567e-05 | 2.8467e-05 | 3.4467e-05 | 3.135e-05 | 2.2133e-05 | 3.1583e-05 | 0.0092367 | 2.34e-05 | 8.185e-05 | 2.4667e-05 | 2.5933e-05 | 0.0001109
[6 empty] | Area iii | 3.0425e-05 | 2.93e-05 | 3.1575e-05 | 2.93e-05 | 2.93e-05 | 2.93e-05 | 0.005395 | 2.93e-05 | 6.51e-05 | 2.93e-05 | 2.93e-05 | 6.86e-05
Area iv
Area v
Area vi
[6 empty] | Averages: | 2.7708e-05 | 2.5883e-05 | 3.2075e-05 | 2.8217e-05 | 2.3772e-05 | 2.7156e-05 | 0.0091467 | 2.4194e-05 | 8.2272e-05 | 2.4867e-05 | 2.5039e-05 | 0.00011345
PR weightings (dredge area averages multiplied by dredge area tonnage)
[6 empty] | Dredge Area | Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[6 empty] | Area i | 1.6987e-05 | 1.2924e-05 | 1.9619e-05 | 1.56e-05 | 1.2924e-05 | 1.3379e-05 | 0.0083254 | 1.2924e-05 | 6.4913e-05 | 1.3412e-05 | 1.2924e-05 | 0.00010455
[6 empty] | Area ii | 7.97e-06 | 8.54e-06 | 1.034e-05 | 9.405e-06 | 6.64e-06 | 9.475e-06 | 0.002771 | 7.02e-06 | 2.4555e-05 | 7.4e-06 | 7.78e-06 | 3.327e-05
[6 empty] | Area iii | 1.5213e-06 | 1.465e-06 | 1.5788e-06 | 1.465e-06 | 1.465e-06 | 1.465e-06 | 0.00026975 | 1.465e-06 | 3.255e-06 | 1.465e-06 | 1.465e-06 | 3.43e-06
Area iv
Area v
Area vi
PR average
Brominated flame retardants as mg/kg wet weight
[7 empty] | 2,2′,4,4′,6-penta- bromodiphenyl ether (BDE100) | Hexabromodiphenyl ether (BDE138) | 2,2′,4,4′,5,5′-hexa- bromodiphenyl ether (BDE153) | 2,2′,4,4′,5,6′-hexa-bromodiphenyl ether (BDE154) | 2,2´,4-tri-bromodiphenylether (BDE17) | 2,2′,3,4,4′,5′,6-heptabromodiphenyl ether (BDE183) | 2,2',3,3',4,4',5,5',6,6'-decabrominated diphenyl ether (BDE 209) | 2,4,4'-tribromodiphenyl ether (BDE28) | 2,2′,4,4′-Tetrabromodiphenyl ether (BDE47) | 2,3',4,4'-Tetrabromodiphenyl ether (BDE66) | 2,2',3,4,4'-Pentabromodiphenyl ether (BDE85) | 2,2',4,4',5-pentabromodiphenyl ether (BDE99)
[7 empty] | 2.6478e-05 | 2.2929e-05 | 3.1538e-05 | 2.647e-05 | 2.1029e-05 | 2.4319e-05 | 0.011366 | 2.1409e-05 | 9.2723e-05 | 2.2277e-05 | 2.2169e-05 | 0.00014125

## PR details (hidden)
PR details: |  |  | Dredge area tonnages:
Application number: | SP2508 |  | Dredge Area | Dredging tonnages | % total dredged material | Total dredged material
Date sampled: | 2025-05-02 |  | Area i | 2015000 | 65% | 3100000
Application title: | DML1946v2 - Marine Application - Port Talbot |  | Area ii | 930000 | 30%
Applicant: | Associated British Ports |  | Area iii | 155000 | 5%
Area iv
Area v
Area vi
PPM (mg/kg)
Metals & Tins | TS% | AS | CD | CR | CU | HG | NI | PB | ZN | DBT | TBT
| 42 | 6.224 | 0.0846 | 13.55 | 8.621 | 0.0562 | 10.97 | 20.28 | 65.78
PPB (ug/kg)
Hydrocarbons |  | ACENAPH | ACENAPT | ANTHRAC | BAA | BAP | BBF | BENZGHI | BEP | BKF | C1N | C1PHEN
|  | 14.6 | 11.8 | 26.8 | 79.7 | 96.6 | 124 | 86.5 | 91.1 | 89.7 | 103 | 105
Hydrocarbons | C2N | C3N | CHRYSEN | DBENZAH | FLUORAN | FLUOREN | INDPYR | NAPTH | PERYLEN | PHENANT | PYRENE | THC (ppm)
| 86.1 | 59.5 | 117 | 20.4 | 159 | 33 | 94.8 | 59.1 | 33.4 | 115 | 124
PPM (mg/kg)
Polychlorinated biphenyls | CB#101 | CB#105 | CB#110 | CB#118 | CB#128 | CB#138 | CB#141 | CB#149 | CB#151
| 0.000468 | 0.000245 | 0.000726 | 0.000674 | 0.000161 | 0.000801 | 0.000143 | 0.000541 | 0.00017
Polychlorinated biphenyls | CB#153 | CB#156 | CB#158 | CB#170 | CB#18 | CB#180 | CB#183 | CB#187 | CB#194
| 0.000914 | 8.4e-05 | 0.000116 | 0.000275 | 0.000475 | 0.000628 | 0.000127 | 0.000345 | 0.000161
Polychlorinated biphenyls | CB#28 | CB#31 | CB#44 | CB#47 | CB#49 | CB#52 | CB#66 | TOT25CBS | TOTICES7
| 0.00119 | 0.000889 | 0.000465 | 0.000192 | 0.000437 | 0.000515 | 0.00105 | 0.0118 | 0.00519
PPM (mg/kg)
Organochlorine pesticides | AHCH | BHCH | GHCH | DIELDRIN | HCB | PPDDE | PPDDT | PPTDE
| 4.2e-05 | 4.2e-05 | 4.2e-05 | 5.48e-05 | 9.89e-05 | 8.61e-05 | 0.000139 | 0.000333
Brominated flame retardants | BDE100 | BDE138 | BDE153 | BDE154 | BDE17 | BDE183 | BDE28 | BDE47
| 2.65e-05 | 2.29e-05 | 3.15e-05 | 2.65e-05 | 2.1e-05 | 2.43e-05 | 2.14e-05 | 9.27e-05
Brominated flame retardants | TS%: BDE66; AS: BDE85; CD: BDE99; HG: BDE209
| 2.23e-05 | 2.22e-05 | 0.000141 |  |  | 0.0114
PSA | TS%: % Gravel; AS: % Sand; CD: % Silt/Clay
| 42.0458 | 0.003447 | 7.5052

## Import (hidden)
ApplicationNo | TS | Gravel | Sand | Silt | As | Cd | Cr | Cu | Hg | Ni | Pb | Zn | DBT | TBT | Acenapth | Acenapthylene | Antracn | BAA | BAP | BBF | BEP | Benzghip | BKF | C1N | C1PHEN | C2N | C3N | Chrysene | Debenzah | Flurant | Fluorene | Indypr | napth | perylene | phenant | pyrene | THC | PCB28 | PCB52 | PCB101 | PCB118 | PCB138 | PCB153 | PCB18 | PCB105 | PCB110 | PCB128 | PCB141 | PCB149 | PCB151 | PCB156 | PCB158 | PCB170 | PCB180 | PCB183 | PCB187 | PCB194 | PCB31 | PCB44 | PCB47 | PCB49 | PCB66 | ICES7 | AHCH | BHCH | GHCH | DIELDRIN | HCB | DDE | DDT | TDE | BDE100 | BDE138 | BDE153 | BDE154 | BDE17 | BDE183 | BDE209 | BDE28 | BDE47 | BDE66 | BDE85 | BDE99 | Ag | No. exempt from chemical analysis | Tonnes exempt
SP2508 | 42 | 42.0458 | 0.003447 | 7.5052 | 6.224 | 0.0846 | 13.55 | 8.621 | 0.0562 | 10.97 | 20.28 | 65.78 |  |  | 14.6 | 11.8 | 26.8 | 79.7 | 96.6 | 124 | 91.1 | 86.5 | 89.7 | 103 | 105 | 86.1 | 59.5 | 117 | 20.4 | 159 | 33 | 94.8 | 59.1 | 33.4 | 115 | 124 |  | 0.00119 | 0.000515 | 0.000468 | 0.000674 | 0.000801 | 0.000914 | 0.000475 | 0.000245 | 0.000726 | 0.000161 | 0.000143 | 0.000541 | 0.00017 | 8.4e-05 | 0.000116 | 0.000275 | 0.000628 | 0.000127 | 0.000345 | 0.000161 | 0.000889 | 0.000465 | 0.000192 | 0.000437 | 0.00105 | 0.00519 | 4.2e-05 | 4.2e-05 | 4.2e-05 | 5.48e-05 | 9.89e-05 | 8.61e-05 | 0.000139 | 0.000333 | 2.65e-05 | 2.29e-05 | 3.15e-05 | 2.65e-05 | 2.1e-05 | 2.43e-05 | 0.0114 | 2.14e-05 | 9.27e-05 | 2.23e-05 | 2.22e-05 | 0.000141 |  | 0 | 0