## Report
Biffa Waste Services
Trecatti Landfill Site
Annual Monitoring Review
January - December 2024
As required by condition 4.2.1 of Permit RP3733PC/V013 for Trecatti Landfill, the operator is required to complete an annual review of monitoring data.
The annual review will be based on the monitoring results that the permit requires the operator to undertake, which for the purposes of this report will run from January to December 2024. Biffa's monitoring is either carried out by ourselves, Lucion or ALS laboratories. Biogenie's surface water testing is carried out by Chemtest.
The review is split into 9 sections;
1. Surface Water
2. Leachate
3. Treated Effluent
4. Groundwater
5. FID
6. Perimeter Gas
7. Gas Compound
8. Dust and Asbestos
9. Biogenie
The full download of environmental monitoring data for 2024 can be viewed in Appendix A (all comments from the laboratory results have been included in the previous quarterly reports)
Drawings in the appendix include:
T3029700-Void Survey
Trecatti Settlement Survey T3063400
T3180804- Surface Emissions
Trecatti T3180120 MEPP
Void Capacity
Between July 2024 – January 2025, 171.914m3 of void has been consumed, with the remaining void in January 2024 calculated as approximately 4,875,437m3 for the site to be completed to final levels.
Settlement Behaviour
The landfill settlement over the last year at Trecatti Landfill shows an average of -0.073m across the site. Modelling of the settlement of landfilled waste, both in duration and quantum, is difficult to complete with any certainty due to the complex and variable parameters that contribute to the settlement process. Settlement in landfilled waste is subject to a number of factors, including loading, type of waste, depth of waste and other processes including chemical and microbial actions. These processes appear as time-dependent, and are also influenced by factors such as leachate composition, pH, temperature and moisture. The settlement of waste over time comprises of two main elements: Primary or immediate settlement - this is load related and primary drivers are the expulsion of air and liquid from the waste resulting in consolidation. The rate of settlement is dependent on the depth of waste and the type of waste (and the amount of air/liquid contained therein). This is active during waste filling and immediately following completion of waste tipping. Secondary settlement – this is typically considered following post closure or cessation of tipping, and is initially a product of physio-chemical and mechanical creep (deformation due to load stresses) and then biological decomposition of the waste. These actions result in slow gradual settlement over a long period of time, typically many decades. Landfill settlement, due to the aforementioned factors, does vary considerably and can be as high as 40%.
1. Surface Water
The permit requires surface water discharge to be sampled and recorded monthly and to test for the following contaminants: pH / Ammoniacal Nitrogen / Suspended Solids / Chemical Oxygen Demand
Following an Environment Agency audit on surface water management carried out on 16th May 2008, and subsequently approved on 30th July 2008, the monitoring points have been amended as follows: · SWA (81702001) - Northwest boundary discharge point · SWB (81702002) - East boundary discharge point · SWC (81702003) - North boundary upstream point During the audit it was agreed that as the operator is unable to control external influences on the monitoring points the rate of flow and volume permit requirements would be removed. However, the volume of surface water pumped off site to SWA would be reported. From January to December 2024, approximately ###### m3 of surface water was pumped off site. This figure is to be confirmed and will be submitted separately
Results for SWA and SWB for the reporting period are shown in the tables below. All points were in compliance over the year.
Table 1: SWA quality results
SWA | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit Limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
January | 7.5 | 63 | 3.04 | 16
February | 7.7 | 12 | 2.07 | 35
March | 7.4 | 7 | 2.57 | 33
April | Insufficient Sample
May | Insufficient Sample
June | 7.7 | 4 | 1.89 | 22
July
August | 7.9 | 7 | 2.16 | 56
September | Insufficient Sample
October | Insufficient Sample
November | 7.7 | 6 | 2.02 | 13
December | 7.5 | 10 | 3.79 | 14
Table 2: SWB quality results
SWB | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit Limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
January | 7.7 | 2 | <0.06 | 32
February | 6.7 | 6 | 0.27 | <11.0
March | 7.5 | 8 | <0.06 | 30
April | Insufficient Sample
May | Insufficient Sample
June | 8 | 6 | 0.14 | 19
July | Insufficient Sample
August | SEE A/C | 3 | 0.17 | 46
September | Insufficient Sample
October | Insufficient Sample
November | 7.6 | 2 | <0.06 | 18
December | 7.6 | 2 | <0.06 | 30
SWA and SWB were dry for periodic times throughout the year even during times of prolonged rainfall the flow rates were very low. All of the surface water monitoring points are impacted by external influences, namely the neighbouring agricultural land, therefore the samples taken are not fully representative of the site's surface water quality.
• All permanent engineering works (lining and capping/restoration) will continue to consider the impact of the works on surface water management during the design, construction and post-construction stages. This will include the provision of temporary storage lagoons, bunds, rain-flaps, ditches and pumping stations and pipelines. All permanent construction work will be the subject of independent CQA supervision. • All temporary engineering works (temporary capping) will consider the impact of surface water and may require the construction of rain-flaps and lined ditches to shed uncontaminated surface water into perimeter drainage ditches or temporary storage lagoons. • In order to reduce the build up of suspended solids within surface water bodies and water courses, any bare soil flanks and restored areas will be seeded with a suitable grass mix as soon as practicable in order to stabilise flanks, encourage infiltration and reduce surface run-off. This will be inspected and reseeded if necessary. • Spot sampling will be undertaken by the Environmental and Gas Operative in the site laboratory prior to any surface water being pumped to the perimeter ditch. • V-notch weirs are installed upstream of the surface water discharge points in order to slow down the flow of water to encourage the settlement of suspended solids prior to discharge. These features will be cleaned and maintained on a quarterly basis and recorded on the critical plant schedule. • Perimeter surface water ditches, lagoons and other site drainage outlets will be inspected on a weekly basis and recorded in the site diary. •Road sweeper to be employed a minimum of twice a week. On periods of increased activity or poor weather conditions a road sweeper will be used more frequently or when the wheel wash is non-operational for a long period. This is left to the manager’s discretion. • Site to have a fully operational wheel wash, which will be cleaned every six months. A spare wheel wash pump will be held at site to replace immediately if the current pump fails, reducing down time. The wheel wash is part of the critical plant list, which is reviewed monthly to ensure it is maintained as per schedule. The wheel wash may be cleaned more frequently depending on the manager’s findings during his/her monthly compliance inspection. All site users driving vehicles are instructed that they must use this facility before leaving site. Persistent misuse of the wheel wash by lorry drivers will lead to the driver being banned. • All waste vehicles must be sheeted upon arrival at Trecatti. De-sheeting must only take place in designated de-sheeting bay. • Vehicle check areas must be used by all drivers before leaving site so they can clean any excessive debris off their vehicles and remove any stones which may have been caught within their tyres whilst travelling over site.
2. Leachate
2.1 Leachate Quality
The permit requires the operator to sample leachate quarterly for the following components; pH / Ammoniacal Nitrogen / Chloride / Total Alkalinity / BOD / COD / TOC / TON / Iron / Chromium / Copper / Lead / Zinc / Nickel / Cadmium / Magnesium / Potassium / Sulphate / Calcium / Sodium / Manganese / Mecoprop / Toluene / Xylene / Naphthalene. The permit requires an annual suite that also includes hazardous substances. There are however no limits set up in the permit with which the leachate samples must comply, but they have been reviewed and are as expected. Although we endeavour to meet all of the permit reporting requirements we are not always able to obtain a sample from every leachate well each quarter. This is due to tipping operations or maintenance works being carried out on the wells.
2.2 Leachate Levels
The permit requires the operator to report leachate levels from specified points at monthly intervals. Trend graphs for the reporting period are shown below.
2024 | LW1 | LW2 | LW3 | LW4 | LW5 | LW6 | LW7 | LW8 | Compliance Limit LW1,2, 3, 4, 7 & 8 (m) | Compliance Limit LW5,6 (m)
Jan | 23.87 | 25.59 | 28.8 | 53.48 | 4.01 | 4.76 | 19.49 | 32.72 | 33 | 5
Feb | 25.87 | 28.64 | 29.04 | 53.28 | 3.55 | 4.34 | 20.56 | 32.36 | 33 | 5
Mar | 26.98 | 31.59 | 31.82 | 52.02 | 4.22 | 4.67 | 20.99 | 32.81 | 33 | 5
Apr | 36.83 | 34.67 | 28.92 | 54.12 | 4.1 | 4.993 | 33.99 | 47.81 | 33 | 5
May | 25.98 | 30.15 | 32.13 | 52.93 | 2.79 | 3.55 | 16.54 | 30.04 | 33 | 5
Jun | 26.08 | 27.47 | 30.02 | 54.37 | 3.77 | 4.33 | 21.65 | 35.37 | 33 | 5
Jul | 26.21 | 28.6 | 28.81 | 53.81 | 3.9 | 4.3 | 21.54 | 32.15 | 33 | 5
Aug | 25.81 | 28.7 | 30.15 | 51.7 | 3.24 | 4.2 | 20.11 | 30.14 | 33 | 5
Sep | 28.51 | 28.59 | 27.81 | 54.7 | 2.68 | 3.88 | 20.98 | 32.81 | 33 | 5
Oct | 27.22 | 29.69 | 31.24 | 54.37 | 4.01 | 3.98 | 21.65 | 31.49 | 33 | 5
Nov | 25.21 | 28.38 | 29.13 | 51.7 | 3.44 | 4.3 | 19.67 | 30.04 | 33 | 5
Dec | 25.98 | 34.59 | 32.13 | 45.81 | 2.9 | 4.11 | 20.89 | 42.27 | 33 | 5
Leachate levels in LW1, LW2, LW4, LW7 and LW8 were non-compliant in the course of 2024. Site has experienced elevated levels which have been attributed to the wells location within the operational site and the infrastructure pumping being suspended. The treatment plant continues to run with similar volumes treated compared with last year. LW4 has undergone repair work and the level is now on a downward trend.
3. Treated Effluent
During this period 95,124.00 m3 of treated leachate was discharged to the sewer. The treated effluent is sampled and recorded monthly and tested for the following determinants: pH / Suspended Solids / Ammoniacal Nitrogen / Temperature / Total Metals / Cyanide / Sulphide / Sulphate
Table 3 Treated effluent results for 2024
81703400 | pH | Suspended Solids | Cyanide | Sulphide | Sulphate | Dissolved Methane | Phosphate | Ammoniacal Nitrogen | COD | Total Metals
Discharge Limit | 6 to 11 | 400mg/l | 0.2mg/l | 1mg/l | 1000mg/l | 0.14mg/l | 10mg/l | 40mg/l | 2000mg/l | 1mg/l
January | 7 | 60 | 0.055 | 0.02 | 113 | <0.010 | 1.98 | <0.41 | 477 | 0.171
February | 6 | 46 | 0.013 | <0.020 | 118 | <0.010 | 2.4 | 11.1 | 448 | 0.328
March | 6.9 | 95 | 0.014 | <0.020 | 118 | <0.010 | 2.43 | 2.71 | 589 | 0.259
April | 7 | 51 | 0.015 | <0.020 | 114 | <0.010 | 2.31 | 0.43 | 486 | 0.128
May | Unable to sample due to maintenance issues
June | 7.4 | 41 | 0.058 | <0.020 | 105 | <0.010 | 2.22 | 2.74 | 392 | 0.102
July | 7.5 | 109 | 0.09 | 0.06 | 86.7 | <0.010 | 4.24 | <0.41 | 608 | 0.129
August | 7.9 | 33 | 0.046 | <0.020 | 15.3 | <0.010 | 0.973 | 38.2 | 166 | 0.027
September | sample misplaced by courier
October | 7.5 | 96 | 0.044 | <0.020 | 84.1 | <0.010 | 2.11 | <0.41 | 439 | 0.092
November | 7.5 | 118 | 0.064 | 0.03 | 132 | <0.010 | 1.66 | 4.31 | 601 | 0.236
December | 7.1 | 97 | 0.024 | <0.020 | 217 | <0.010 | 1.08 | 9.81 | 157 | 0.212
All parameters were compliant for the reporting period.
4. Groundwater
4.1 Groundwater Levels
Groundwater levels throughout 2024 showed little variation. The slight level increase recorded towards the last quarter could be seasonal fluctuations. It is also noted that groundwater levels could be influenced by the neighbouring quarry extraction which have ceased groundwater extraction and may need further investigation to understand the impact they may have on the site going forward. GW11 needs further investigation into the sudden elevated levels and a CCTV survey is being organised to understand this change in levels.
Figure 3: Groundwater levels 2022 to 2024
4.2 Groundwater Quality
Annual and quarterly samples were taken from groundwater boreholes: GW1, GW2, GW4, GW6, GW8 and GW12 during the reporting period. Out of the boreholes sampled only GW1, GW2 and GW12 have permit limits associated with them. Site investigations have shown that GW5, GW7, GW9, GW10, GW11 and GW13 have very low groundwater levels and slow recharge rates and therefore cannot be sampled. Figures 4 to 6 show ammoniacal nitrogen, chloride and Mecoprop levels in the groundwater boreholes that could be sampled. Results that were below the limit of detection are represented as 0 on the graphs.
The permit requires the operator to report leachate levels from specified points at monthly intervals. Trend graphs for the reporting period are shown below. LW1: Figure 4: Ammoniacal nitrogen levels in groundwater boreholes | Figure 5: Chloride levels in groundwater boreholes
The permit requires the operator to report leachate levels from specified points at monthly intervals. Trend graphs for the reporting period are shown below. LW1: Figure 6: Mecoprop levels in groundwater boreholes | Figure 7: Cadmium levels in groundwater boreholes
Figure 8: Naphthalene levels in groundwater boreholes
All parameters were compliant during the reporting period. Ammoniacal nitrogen levels were stable in all of the boreholes. GW2 decreased in May 2024 and overall has slightly decreased during the 3 year period. Chloride levels also showed little variation in majority of the boreholes. The exception is with GW8 at the beginning of 2022 the chloride was 784mg/l and this has shown a decreasing trend (479mg/l). Mecoprop levels in GW2 show a decreasing trend. There was a peak in GW4 which was due a raised reporting limit of <0.08ug/l in November 2023. In GW12 the cadmium was a raised reporting limit at 0.007m/g in September 2023. Results for naphthalene, toluene and xylene were below the limit of detection.
5. FID
The site continues to pro-actively monitor surface emissions and the gas extraction system. Regular reviews of this data leads to the installation of temporary capping and gas infrastructure improvements to capture as much landfill gas as possible from the site. The highest readings detected during the year were in December at 40ppm for a peak reading and 15ppm for a steady state. There have been zero complaints during the reporting period. The annual surface emission has been included as a separate attachment, there are some areas highlighted due to them being in open operational areas.
6. Perimeter Gas
At present there are twenty-six gas boreholes located on the outer perimeter of the site. As is well documented for the site there are old mine workings and current mine workings in the locality of the site which make the ground gas around the site complex. This coupled with the old council run Merthyr Waste site adjacent to the current lined Biffa Site make the issue of gas migration in perimeter boreholes difficult to attribute to one specific source.
The gas extraction system is fully maintained, monitored and infrastructure added frequently to ensure the maximum flow off site through the engines and flares is maintained.
Figures 9 to 13 below show the methane and carbon dioxide percentages for the boreholes that exceeded compliance limits in the reporting period. BH4, BH7, BH22 and BH23 have continued to fluctuate in line with historical levels and where there has been incidences of levels above compliance in these boreholes this has not been associated with rising trends, therefore no deterioration in the gas extraction system. There have been instances of BH21 being above there actions limits but still within there trends for the boreholes.
The permit requires the operator to report leachate levels from specified points at monthly intervals. Trend graphs for the reporting period are shown below. LW1: Figure 9: CH4 and CO2 levels in BH4 | Figure 10: CH4 and CO2 levels in BH7
The permit requires the operator to report leachate levels from specified points at monthly intervals. Trend graphs for the reporting period are shown below. LW1: Figure 11: CH4 and CO2 levels in BH21 (Action Limits) | Figure 12: CH4 and CO2 levels in BH22
Figure 13: CH4 and CO2 levels in BH23
7. Gas Compound
| LFG Flared (m3) |  | LFG Used in Engines (m3)
Trecatti | 91926 |  | 12133.255
8. Dust & Asbestos
Dust and Asbestos monitoring is carried out every 6 months. Dust measurements are taken for total inhalable dust and particulate matter <10 microns. The results are a mean over a 24hr period.
All dust and Asbestos results were compliant for the reporting period.
9. Biogenie
Chemtest Ltd carry out the analysis on behalf on Biogenie. Surface water samples are taken monthly from the Biopiles. No samples are taken from the Surface Water Lagoon as it has been integrated into the biogenie water treatment system. Pumping Permits are raised by Biogenie and authorised by Biffa Personnel when they want to pump from the Surface Water Lagoon into the 385 Lagoon and is signed off by Biffa only when the process water is compliant. Non-compliant water is sent to sewer.
No water was discharged during the reporting period.

## Complaints
Year | No. of Compliants
2000 | 244
2001 | 1082
2002 | 782
2003 | 422
2004 | 206
2005 | 191
2006 | 296
2007 | 702
2008 | 101
2009 | 25
2010 | 28
2011 | 65
2012 | 78
2013 | 22
2014 | 77
2015 | 62
2016 | 6
2017 | 5
2018 | 4
2019 | 2
2020 | 4
2021 | 5
2022 | 0
2023 | 1
2024 | 0

## Table S4.3
Table S4.3 Performance Parameters
Parameter | Frequency of assessment | Annual Total | Unit
Water usage |  | 640 | tonnes
Energy used including leachate treatment |  | 517913.1 | MWh
Total raw material used |  | 0 | tonnes
* Raw materials - wood fines used as soil enhancer in STF

## Table S4.2
Table S4.2: Annual Production/treatment
Leachate | cubic metres/year
Disposed of off site
Disposed of onsite effluent treatment plant | 95124 | m3
recirculated into waste mass | n/a
Surface water and/or groundwater | cubic metres/year
Disposed of off site | tbc | m3
Disposed of to effluent treatment plant | n/a
Landfill gas | cubic metres/year
combustion in flares | 91926 | m3
combustion in gas engines | 12133.255 | m3
other methods of gas utilisation | n/a