## INFO
Produced by Envireau Water
P19-247 Cott DC Lic Test Pumping
KEY
Data processing
Charts/Graphs
Raw data
GRID REFERENCE
BH4 | (X:285877, Y:370477)
BH5 | (X:285863,Y:370523)

## Manual & Logged Data
| Date | Count | Flow rate (ltr/hr) | Flow rate (m3/hr) | Temperature (C) | BH5 logged water level (mbd) | BH5 logged water level (mbd) | BH4 logged water level BH4 (mbd) | BH4 logged water level (mbd) | BH4 logged water level (mbd) | BH1 manual water level (mbd) | BH4 manual water level (mbd) | BH5 manual water level (mbd) | Total Elapsed Time t (min) | PBH CRT Elapsed Time (min) | Logged Drawdown BH5 (m) | t/t' | Logged Drawdown BH4 (m)
Start of monitoring | 2019-06-13 20:00 | 0 | 0 | 0 | 10.11 | 0 | 0.77 | 1.55 | 0.396 | 1.696 |  |  |  | 645
| 2019-06-13 20:15 | 0 | 0 | 0 | 10.09 | 0 | 0.77 | 1.539 | 0.407 | 1.707 |  |  |  | 660
| 2019-06-13 20:30 | 0 | 0 | 0 | 10.089 | 0 | 0.77 | 1.552 | 0.394 | 1.694 |  |  |  | 675
| 2019-06-13 20:45 | 0 | 0 | 0 | 10.084 | 0 | 0.77 | 1.538 | 0.408 | 1.708 |  |  |  | 690
| 2019-06-13 21:00 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.538 | 0.408 | 1.708 |  |  |  | 705
| 2019-06-13 21:15 | 0 | 0 | 0 | 10.115 | 0 | 0.77 | 1.536 | 0.41 | 1.71 |  |  |  | 720
| 2019-06-13 21:30 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.532 | 0.414 | 1.714 |  |  |  | 735
| 2019-06-13 21:45 | 0 | 0 | 0 | 10.089 | 0 | 0.77 | 1.534 | 0.412 | 1.712 |  |  |  | 750
| 2019-06-13 22:00 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.537 | 0.409 | 1.709 |  |  |  | 765
| 2019-06-13 22:15 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.539 | 0.407 | 1.707 |  |  |  | 780
| 2019-06-13 22:30 | 0 | 0 | 0 | 10.104 | 0 | 0.77 | 1.535 | 0.411 | 1.711 |  |  |  | 795
| 2019-06-13 22:45 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.522 | 0.424 | 1.724 |  |  |  | 810
| 2019-06-13 23:00 | 0 | 0 | 0 | 10.086 | 0 | 0.77 | 1.537 | 0.409 | 1.709 |  |  |  | 825
| 2019-06-13 23:15 | 0 | 0 | 0 | 10.089 | 0 | 0.77 | 1.527 | 0.419 | 1.719 |  |  |  | 840
| 2019-06-13 23:30 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.532 | 0.414 | 1.714 |  |  |  | 855
| 2019-06-13 23:45 | 0 | 0 | 0 | 10.098 | 0 | 0.77 | 1.535 | 0.411 | 1.711 |  |  |  | 870
| 2019-06-14 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.529 | 0.417 | 1.717 |  |  |  | 885
| 2019-06-14 00:15 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.525 | 0.421 | 1.721 |  |  |  | 900
| 2019-06-14 00:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.531 | 0.415 | 1.715 |  |  |  | 915
| 2019-06-14 00:45 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.536 | 0.41 | 1.71 |  |  |  | 930
| 2019-06-14 01:00 | 0 | 0 | 0 | 10.088 | 0 | 0.77 | 1.533 | 0.413 | 1.713 |  |  |  | 945
| 2019-06-14 01:15 | 0 | 0 | 0 | 10.081 | 0 | 0.77 | 1.533 | 0.413 | 1.713 |  |  |  | 960
| 2019-06-14 01:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.537 | 0.409 | 1.709 |  |  |  | 975
| 2019-06-14 01:45 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.511 | 0.435 | 1.735 |  |  |  | 990
| 2019-06-14 02:00 | 0 | 0 | 0 | 10.086 | 0 | 0.77 | 1.532 | 0.414 | 1.714 |  |  |  | 1005
| 2019-06-14 02:15 | 0 | 0 | 0 | 10.074 | 0 | 0.77 | 1.519 | 0.427 | 1.727 |  |  |  | 1020
| 2019-06-14 02:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.536 | 0.41 | 1.71 |  |  |  | 1035
| 2019-06-14 02:45 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.531 | 0.415 | 1.715 |  |  |  | 1050
| 2019-06-14 03:00 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.541 | 0.405 | 1.705 |  |  |  | 1065
| 2019-06-14 03:15 | 0 | 0 | 0 | 10.087 | 0 | 0.77 | 1.523 | 0.423 | 1.723 |  |  |  | 1080
| 2019-06-14 03:30 | 0 | 0 | 0 | 10.105 | 0 | 0.77 | 1.53 | 0.416 | 1.716 |  |  |  | 1095
| 2019-06-14 03:45 | 0 | 0 | 0 | 10.108 | 0 | 0.77 | 1.526 | 0.42 | 1.72 |  |  |  | 1110
| 2019-06-14 04:00 | 0 | 0 | 0 | 10.105 | 0 | 0.77 | 1.535 | 0.411 | 1.711 |  |  |  | 1125
| 2019-06-14 04:15 | 0 | 0 | 0 | 10.095 | 0 | 0.77 | 1.534 | 0.412 | 1.712 |  |  |  | 1140
| 2019-06-14 04:30 | 0 | 0 | 0 | 10.095 | 0 | 0.77 | 1.525 | 0.421 | 1.721 |  |  |  | 1155
| 2019-06-14 04:45 | 0 | 0 | 0 | 10.11 | 0 | 0.77 | 1.526 | 0.42 | 1.72 |  |  |  | 1170
| 2019-06-14 05:00 | 0 | 0 | 0 | 10.088 | 0 | 0.77 | 1.528 | 0.418 | 1.718 |  |  |  | 1185
| 2019-06-14 05:15 | 0 | 0 | 0 | 10.09 | 0 | 0.77 | 1.522 | 0.424 | 1.724 |  |  |  | 1200
| 2019-06-14 05:30 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.539 | 0.407 | 1.707 |  |  |  | 1215
| 2019-06-14 05:45 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.534 | 0.412 | 1.712 |  |  |  | 1230
| 2019-06-14 06:00 | 0 | 0 | 0 | 10.106 | 0 | 0.77 | 1.531 | 0.415 | 1.715 |  |  |  | 1245
| 2019-06-14 06:15 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.539 | 0.407 | 1.707 |  |  |  | 1260
| 2019-06-14 06:30 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.549 | 0.397 | 1.697 |  |  |  | 1275
| 2019-06-14 06:45 | 0 | 0 | 0 | 10.102 | 0 | 0.77 | 1.545 | 0.401 | 1.701 |  |  |  | 1290
| 2019-06-14 07:00 | 0 | 0 | 0 | 10.116 | 0 | 0.77 | 1.547 | 0.399 | 1.699 |  |  |  | 1305
| 2019-06-14 07:15 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.539 | 0.407 | 1.707 |  |  |  | 1320
| 2019-06-14 07:30 | 0 | 0 | 0 | 10.087 | 0 | 0.77 | 1.533 | 0.413 | 1.713 |  |  |  | 1335
| 2019-06-14 07:45 | 0 | 0 | 0 | 10.092 | 0 | 0.77 | 1.552 | 0.394 | 1.694 |  |  |  | 1350
| 2019-06-14 08:00 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.537 | 0.409 | 1.709 |  |  |  | 1365
| 2019-06-14 08:15 | 0 | 0 | 0 | 10.105 | 0 | 0.77 | 1.543 | 0.403 | 1.703 |  |  |  | 1380
| 2019-06-14 08:30 | 0 | 0 | 0 | 10.081 | 0 | 0.77 | 1.551 | 0.395 | 1.695 |  |  |  | 1395
| 2019-06-14 08:45 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.537 | 0.409 | 1.709 |  |  |  | 1410
| 2019-06-14 09:00 | 0 | 0 | 0 | 10.108 | 0 | 0.77 | 1.55 | 0.396 | 1.696 | 0.04 | 1.56 | 0.77 | 1425
| 2019-06-14 09:15 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.553 | 0.393 | 1.693 |  |  |  | 1440
| 2019-06-14 09:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.55 | 0.396 | 1.696 |  |  |  | 1455
| 2019-06-14 09:45 | 0 | 0 | 0 | 10.118 | 0 | 0.77 | 1.545 | 0.401 | 1.701 |  |  |  | 1470
| 2019-06-14 10:15 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.555 | 0.391 | 1.691 |  |  |  | 1485
| 2019-06-14 10:30 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.541 | 0.405 | 1.705 |  |  |  | 1500
| 2019-06-14 10:00 | 0 | 0 | 0 | 10.093 | 0 | 0.77 | 1.547 | 0.399 | 1.699 |  |  |  | 1515
| 2019-06-14 10:45 | 0 | 0 | 0 | 10.098 | 0 | 0.77 | 1.556 | 0.39 | 1.69 |  |  |  | 1530
| 2019-06-14 11:00 | 0 | 0 | 0 | 10.087 | 0 | 0.77 | 1.555 | 0.391 | 1.691 |  |  |  | 1545
| 2019-06-14 11:15 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.549 | 0.397 | 1.697 |  |  |  | 1560
| 2019-06-14 11:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.555 | 0.391 | 1.691 |  |  |  | 1575
| 2019-06-14 11:45 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.567 | 0.379 | 1.679 |  |  |  | 1590
| 2019-06-14 12:00 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.567 | 0.379 | 1.679 |  |  |  | 1605
| 2019-06-14 12:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.546 | 0.4 | 1.7 |  |  |  | 1620
| 2019-06-14 12:45 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.557 | 0.389 | 1.689 |  |  |  | 1635
| 2019-06-14 13:00 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.564 | 0.382 | 1.682 |  |  |  | 1650
| 2019-06-14 13:15 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.559 | 0.387 | 1.687 |  |  |  | 1665
| 2019-06-14 13:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.558 | 0.388 | 1.688 |  |  |  | 1680
| 2019-06-14 13:45 | 0 | 0 | 0 | 10.095 | 0 | 0.77 | 1.56 | 0.386 | 1.686 |  |  |  | 1695
| 2019-06-14 14:00 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.562 | 0.384 | 1.684 |  |  |  | 1710
| 2019-06-14 14:15 | 0 | 0 | 0 | 10.088 | 0 | 0.77 | 1.556 | 0.39 | 1.69 |  |  |  | 1725
| 2019-06-14 14:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.557 | 0.389 | 1.689 |  |  |  | 1740
| 2019-06-14 14:45 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.566 | 0.38 | 1.68 |  |  |  | 1755
| 2019-06-14 15:00 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.569 | 0.377 | 1.677 |  |  |  | 1770
| 2019-06-14 15:15 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.561 | 0.385 | 1.685 |  |  |  | 1785
| 2019-06-14 15:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.577 | 0.369 | 1.669 |  |  |  | 1800
| 2019-06-14 15:45 | 0 | 0 | 0 | 10.101 | 0 | 0.77 | 1.56 | 0.386 | 1.686 |  |  |  | 1815
| 2019-06-14 16:00 | 0 | 0 | 0 | 10.106 | 0 | 0.77 | 1.58 | 0.366 | 1.666 |  |  |  | 1830
| 2019-06-14 16:15 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.581 | 0.365 | 1.665 |  |  |  | 1845
| 2019-06-14 16:30 | 0 | 0 | 0 | 10.117 | 0 | 0.77 | 1.565 | 0.381 | 1.681 |  |  |  | 1860
| 2019-06-14 16:45 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.582 | 0.364 | 1.664 |  |  |  | 1875
| 2019-06-14 17:00 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.57 | 0.376 | 1.676 |  |  |  | 1890
| 2019-06-14 17:15 | 0 | 0 | 0 | 10.102 | 0 | 0.77 | 1.579 | 0.367 | 1.667 |  |  |  | 1905
| 2019-06-14 17:30 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.582 | 0.364 | 1.664 |  |  |  | 1920
| 2019-06-14 17:45 | 0 | 0 | 0 | 10.08 | 0 | 0.77 | 1.592 | 0.354 | 1.654 |  |  |  | 1935
| 2019-06-14 18:00 | 0 | 0 | 0 | 10.109 | 0 | 0.77 | 1.578 | 0.368 | 1.668 |  |  |  | 1950
| 2019-06-14 18:15 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.579 | 0.367 | 1.667 |  |  |  | 1965
| 2019-06-14 18:30 | 0 | 0 | 0 | 10.102 | 0 | 0.77 | 1.579 | 0.367 | 1.667 |  |  |  | 1980
| 2019-06-14 18:45 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.579 | 0.367 | 1.667 |  |  |  | 1995
| 2019-06-14 19:00 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.592 | 0.354 | 1.654 |  |  |  | 2010
| 2019-06-14 19:15 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.584 | 0.362 | 1.662 |  |  |  | 2025
| 2019-06-14 19:30 | 0 | 0 | 0 | 10.086 | 0 | 0.77 | 1.587 | 0.359 | 1.659 |  |  |  | 2040
| 2019-06-14 19:45 | 0 | 0 | 0 | 10.105 | 0 | 0.77 | 1.591 | 0.355 | 1.655 |  |  |  | 2055
| 2019-06-14 20:00 | 0 | 0 | 0 | 10.112 | 0 | 0.77 | 1.59 | 0.356 | 1.656 |  |  |  | 2070
| 2019-06-14 20:15 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.597 | 0.349 | 1.649 |  |  |  | 2085
| 2019-06-14 20:30 | 0 | 0 | 0 | 10.118 | 0 | 0.77 | 1.595 | 0.351 | 1.651 |  |  |  | 2100
| 2019-06-14 20:45 | 0 | 0 | 0 | 10.082 | 0 | 0.77 | 1.593 | 0.353 | 1.653 |  |  |  | 2115
| 2019-06-14 21:00 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.59 | 0.356 | 1.656 |  |  |  | 2130
| 2019-06-14 21:15 | 0 | 0 | 0 | 10.118 | 0 | 0.77 | 1.598 | 0.348 | 1.648 |  |  |  | 2145
| 2019-06-14 21:30 | 0 | 0 | 0 | 10.078 | 0 | 0.77 | 1.608 | 0.338 | 1.638 |  |  |  | 2160
| 2019-06-14 21:45 | 0 | 0 | 0 | 10.119 | 0 | 0.77 | 1.613 | 0.333 | 1.633 |  |  |  | 2175
| 2019-06-14 22:00 | 0 | 0 | 0 | 10.105 | 0 | 0.77 | 1.608 | 0.338 | 1.638 |  |  |  | 2190
| 2019-06-14 22:15 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.609 | 0.337 | 1.637 |  |  |  | 2205
| 2019-06-14 22:30 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.61 | 0.336 | 1.636 |  |  |  | 2220
| 2019-06-14 22:45 | 0 | 0 | 0 | 10.104 | 0 | 0.77 | 1.614 | 0.332 | 1.632 |  |  |  | 2235
| 2019-06-14 23:00 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.619 | 0.327 | 1.627 |  |  |  | 2250
| 2019-06-14 23:15 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.616 | 0.33 | 1.63 |  |  |  | 2265
| 2019-06-14 23:30 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.606 | 0.34 | 1.64 |  |  |  | 2280
| 2019-06-14 23:45 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.616 | 0.33 | 1.63 |  |  |  | 2295
| 2019-06-15 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.607 | 0.339 | 1.639 |  |  |  | 2310
| 2019-06-15 00:15 | 0 | 0 | 0 | 10.092 | 0 | 0.77 | 1.618 | 0.328 | 1.628 |  |  |  | 2325
| 2019-06-15 00:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.617 | 0.329 | 1.629 |  |  |  | 2340
| 2019-06-15 00:45 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.618 | 0.328 | 1.628 |  |  |  | 2355
| 2019-06-15 01:00 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.624 | 0.322 | 1.622 |  |  |  | 2370
| 2019-06-15 01:15 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.625 | 0.321 | 1.621 |  |  |  | 2385
| 2019-06-15 01:30 | 0 | 0 | 0 | 10.109 | 0 | 0.77 | 1.624 | 0.322 | 1.622 |  |  |  | 2400
| 2019-06-15 01:45 | 0 | 0 | 0 | 10.103 | 0 | 0.77 | 1.632 | 0.314 | 1.614 |  |  |  | 2415
| 2019-06-15 02:00 | 0 | 0 | 0 | 10.106 | 0 | 0.77 | 1.618 | 0.328 | 1.628 |  |  |  | 2430
| 2019-06-15 02:15 | 0 | 0 | 0 | 10.077 | 0 | 0.77 | 1.639 | 0.307 | 1.607 |  |  |  | 2445
| 2019-06-15 02:30 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.637 | 0.309 | 1.609 |  |  |  | 2460
| 2019-06-15 02:45 | 0 | 0 | 0 | 10.112 | 0 | 0.77 | 1.644 | 0.302 | 1.602 |  |  |  | 2475
| 2019-06-15 03:00 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.621 | 0.325 | 1.625 |  |  |  | 2490
| 2019-06-15 03:15 | 0 | 0 | 0 | 10.114 | 0 | 0.77 | 1.62 | 0.326 | 1.626 |  |  |  | 2505
| 2019-06-15 03:30 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.626 | 0.32 | 1.62 |  |  |  | 2520
| 2019-06-15 03:45 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.636 | 0.31 | 1.61 |  |  |  | 2535
| 2019-06-15 04:00 | 0 | 0 | 0 | 10.104 | 0 | 0.77 | 1.633 | 0.313 | 1.613 |  |  |  | 2550
| 2019-06-15 04:15 | 0 | 0 | 0 | 10.123 | 0 | 0.77 | 1.631 | 0.315 | 1.615 |  |  |  | 2565
| 2019-06-15 04:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.638 | 0.308 | 1.608 |  |  |  | 2580
| 2019-06-15 04:45 | 0 | 0 | 0 | 10.083 | 0 | 0.77 | 1.641 | 0.305 | 1.605 |  |  |  | 2595
| 2019-06-15 05:00 | 0 | 0 | 0 | 10.121 | 0 | 0.77 | 1.632 | 0.314 | 1.614 |  |  |  | 2610
| 2019-06-15 05:15 | 0 | 0 | 0 | 10.101 | 0 | 0.77 | 1.63 | 0.316 | 1.616 |  |  |  | 2625
| 2019-06-15 05:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.639 | 0.307 | 1.607 |  |  |  | 2640
| 2019-06-15 05:45 | 0 | 0 | 0 | 10.11 | 0 | 0.77 | 1.642 | 0.304 | 1.604 |  |  |  | 2655
| 2019-06-15 06:00 | 0 | 0 | 0 | 10.086 | 0 | 0.77 | 1.643 | 0.303 | 1.603 |  |  |  | 2670
| 2019-06-15 06:15 | 0 | 0 | 0 | 10.09 | 0 | 0.77 | 1.657 | 0.289 | 1.589 |  |  |  | 2685
| 2019-06-15 06:30 | 0 | 0 | 0 | 10.111 | 0 | 0.77 | 1.637 | 0.309 | 1.609 |  |  |  | 2700
| 2019-06-15 06:45 | 0 | 0 | 0 | 10.096 | 0 | 0.77 | 1.646 | 0.3 | 1.6 |  |  |  | 2715
| 2019-06-15 07:00 | 0 | 0 | 0 | 10.104 | 0 | 0.77 | 1.64 | 0.306 | 1.606 |  |  |  | 2730
| 2019-06-15 07:15 | 0 | 0 | 0 | 10.108 | 0 | 0.77 | 1.646 | 0.3 | 1.6 |  |  |  | 2745
| 2019-06-15 07:30 | 0 | 0 | 0 | 10.089 | 0 | 0.77 | 1.658 | 0.288 | 1.588 |  |  |  | 2760
| 2019-06-15 07:45 | 0 | 0 | 0 | 10.093 | 0 | 0.77 | 1.649 | 0.297 | 1.597 |  |  |  | 2775
| 2019-06-15 08:00 | 0 | 0 | 0 | 10.108 | 0 | 0.77 | 1.655 | 0.291 | 1.591 |  |  |  | 2790
| 2019-06-15 08:15 | 0 | 0 | 0 | 10.1 | 0 | 0.77 | 1.648 | 0.298 | 1.598 |  |  |  | 2805
| 2019-06-15 08:30 | 0 | 0 | 0 | 10.094 | 0 | 0.77 | 1.646 | 0.3 | 1.6 |  |  |  | 2820
| 2019-06-15 08:45 | 0 | 0 | 0 | 10.091 | 0 | 0.77 | 1.647 | 0.299 | 1.599 |  |  |  | 2835
| 2019-06-15 09:00 | 0 | 0 | 0 | 10.099 | 0 | 0.77 | 1.661 | 0.285 | 1.585 | 0 | 1.54 | 0.77 | 2850
| 2019-06-15 09:15 | 0 | 0 | 0 | 10.095 | 0 | 0.77 | 1.658 | 0.288 | 1.588 |  |  |  | 2865
| 2019-06-15 09:30 | 0 | 0 | 0 | 10.097 | 0 | 0.77 | 1.662 | 0.284 | 1.584 |  |  |  | 2880
| 2019-06-15 09:45 | 0 | 0 | 0 | 10.085 | 0 | 0.77 | 1.671 | 0.275 | 1.575 |  |  |  | 2895
Start of pumping - CRT | 2019-06-15 10:00 | 116 | 1392 | 1.392 | 10.105 | 0 | 0.77 | 1.66 | 0.286 | 1.586 |  |  |  | 2910 | 0 | 0
| 2019-06-15 10:15 | 161 | 1932 | 1.932 | 10.081 | 8.079 | 8.849 | 1.681 | 0.265 | 1.565 |  |  |  | 2925 | 15 | 8.079 |  | 0
15/06/2019 10:00 to 17/06/2019 8:30 | 2019-06-15 10:30 | 155 | 1860 | 1.86 | 10.095 | 9.876 | 10.646 | 1.492 | 0.454 | 1.754 |  |  |  | 2940 | 30 | 9.876 |  | 0.189
| 2019-06-15 10:45 | 148 | 1776 | 1.776 | 10.115 | 13.308 | 14.078 | 1.427 | 0.519 | 1.819 |  |  |  | 2955 | 45 | 13.308 |  | 0.254
| 2019-06-15 11:00 | 145 | 1740 | 1.74 | 10.14 | 15.366 | 16.136 | 1.427 | 0.519 | 1.819 |  |  |  | 2970 | 60 | 15.366 |  | 0.254
| 2019-06-15 11:15 | 142 | 1704 | 1.704 | 10.148 | 16.707 | 17.477 | 1.405 | 0.541 | 1.841 |  |  |  | 2985 | 75 | 16.707 |  | 0.276
| 2019-06-15 11:30 | 140 | 1680 | 1.68 | 10.137 | 17.683 | 18.453 | 1.406 | 0.54 | 1.84 |  |  |  | 3000 | 90 | 17.683 |  | 0.275
| 2019-06-15 11:45 | 139 | 1668 | 1.668 | 10.114 | 18.379 | 19.149 | 1.424 | 0.522 | 1.822 |  |  |  | 3015 | 105 | 18.379 |  | 0.257
| 2019-06-15 12:00 | 138 | 1656 | 1.656 | 10.123 | 18.946 | 19.716 | 1.413 | 0.533 | 1.833 |  |  |  | 3030 | 120 | 18.946 |  | 0.268
| 2019-06-15 12:15 | 137 | 1644 | 1.644 | 10.126 | 19.388 | 20.158 | 1.4 | 0.546 | 1.846 |  |  |  | 3045 | 135 | 19.388 |  | 0.281
| 2019-06-15 12:30 | 137 | 1644 | 1.644 | 10.102 | 19.758 | 20.528 | 1.411 | 0.535 | 1.835 |  |  |  | 3060 | 150 | 19.758 |  | 0.27
| 2019-06-15 12:45 | 137 | 1644 | 1.644 | 10.103 | 20.099 | 20.869 | 1.409 | 0.537 | 1.837 |  |  |  | 3075 | 165 | 20.099 |  | 0.272
| 2019-06-15 13:00 | 137 | 1644 | 1.644 | 10.101 | 20.329 | 21.099 | 1.4 | 0.546 | 1.846 |  |  |  | 3090 | 180 | 20.329 |  | 0.281
| 2019-06-15 13:15 | 135 | 1620 | 1.62 | 10.123 | 20.567 | 21.337 | 1.408 | 0.538 | 1.838 |  |  |  | 3105 | 195 | 20.567 |  | 0.273
| 2019-06-15 13:30 | 136 | 1632 | 1.632 | 10.112 | 20.763 | 21.533 | 1.413 | 0.533 | 1.833 |  |  |  | 3120 | 210 | 20.763 |  | 0.268
| 2019-06-15 13:45 | 136 | 1632 | 1.632 | 10.11 | 20.949 | 21.719 | 1.411 | 0.535 | 1.835 |  |  |  | 3135 | 225 | 20.949 |  | 0.27
| 2019-06-15 14:00 | 135 | 1620 | 1.62 | 10.103 | 21.13 | 21.9 | 1.413 | 0.533 | 1.833 |  |  |  | 3150 | 240 | 21.13 |  | 0.268
| 2019-06-15 14:15 | 136 | 1632 | 1.632 | 10.126 | 21.269 | 22.039 | 1.42 | 0.526 | 1.826 |  |  |  | 3165 | 255 | 21.269 |  | 0.261
| 2019-06-15 14:30 | 135 | 1620 | 1.62 | 10.091 | 21.395 | 22.165 | 1.409 | 0.537 | 1.837 |  |  |  | 3180 | 270 | 21.395 |  | 0.272
| 2019-06-15 14:45 | 135 | 1620 | 1.62 | 10.105 | 21.495 | 22.265 | 1.414 | 0.532 | 1.832 |  |  |  | 3195 | 285 | 21.495 |  | 0.267
| 2019-06-15 15:00 | 135 | 1620 | 1.62 | 10.088 | 21.567 | 22.337 | 1.409 | 0.537 | 1.837 |  |  |  | 3210 | 300 | 21.567 |  | 0.272
| 2019-06-15 15:15 | 135 | 1620 | 1.62 | 10.108 | 21.643 | 22.413 | 1.414 | 0.532 | 1.832 |  |  |  | 3225 | 315 | 21.643 |  | 0.267
| 2019-06-15 15:30 | 134 | 1608 | 1.608 | 10.103 | 21.692 | 22.462 | 1.413 | 0.533 | 1.833 |  |  |  | 3240 | 330 | 21.692 |  | 0.268
| 2019-06-15 15:45 | 135 | 1620 | 1.62 | 10.114 | 21.761 | 22.531 | 1.421 | 0.525 | 1.825 |  |  |  | 3255 | 345 | 21.761 |  | 0.26
| 2019-06-15 16:00 | 134 | 1608 | 1.608 | 10.094 | 21.817 | 22.587 | 1.413 | 0.533 | 1.833 |  |  |  | 3270 | 360 | 21.817 |  | 0.268
| 2019-06-15 16:15 | 134 | 1608 | 1.608 | 10.103 | 21.842 | 22.612 | 1.413 | 0.533 | 1.833 |  |  |  | 3285 | 375 | 21.842 |  | 0.268
| 2019-06-15 16:30 | 134 | 1608 | 1.608 | 10.105 | 21.869 | 22.639 | 1.413 | 0.533 | 1.833 |  |  |  | 3300 | 390 | 21.869 |  | 0.268
| 2019-06-15 16:45 | 134 | 1608 | 1.608 | 10.112 | 21.881 | 22.651 | 1.412 | 0.534 | 1.834 |  |  |  | 3315 | 405 | 21.881 |  | 0.269
| 2019-06-15 17:00 | 134 | 1608 | 1.608 | 10.088 | 21.909 | 22.679 | 1.416 | 0.53 | 1.83 |  |  |  | 3330 | 420 | 21.909 |  | 0.265
| 2019-06-15 17:15 | 134 | 1608 | 1.608 | 10.07 | 21.942 | 22.712 | 1.408 | 0.538 | 1.838 |  |  |  | 3345 | 435 | 21.942 |  | 0.273
| 2019-06-15 17:30 | 134 | 1608 | 1.608 | 10.099 | 21.978 | 22.748 | 1.416 | 0.53 | 1.83 |  |  |  | 3360 | 450 | 21.978 |  | 0.265
| 2019-06-15 17:45 | 133 | 1596 | 1.596 | 10.094 | 22.003 | 22.773 | 1.414 | 0.532 | 1.832 |  |  |  | 3375 | 465 | 22.003 |  | 0.267
| 2019-06-15 18:00 | 133 | 1596 | 1.596 | 10.095 | 22.016 | 22.786 | 1.426 | 0.52 | 1.82 |  |  |  | 3390 | 480 | 22.016 |  | 0.255
| 2019-06-15 18:15 | 133 | 1596 | 1.596 | 10.088 | 22.043 | 22.813 | 1.419 | 0.527 | 1.827 |  |  |  | 3405 | 495 | 22.043 |  | 0.262
| 2019-06-15 18:30 | 134 | 1608 | 1.608 | 10.11 | 22.072 | 22.842 | 1.416 | 0.53 | 1.83 |  |  |  | 3420 | 510 | 22.072 |  | 0.265
| 2019-06-15 18:45 | 134 | 1608 | 1.608 | 10.091 | 22.087 | 22.857 | 1.419 | 0.527 | 1.827 |  |  |  | 3435 | 525 | 22.087 |  | 0.262
| 2019-06-15 19:00 | 134 | 1608 | 1.608 | 10.09 | 22.112 | 22.882 | 1.414 | 0.532 | 1.832 |  |  |  | 3450 | 540 | 22.112 |  | 0.267
| 2019-06-15 19:15 | 133 | 1596 | 1.596 | 10.095 | 22.128 | 22.898 | 1.428 | 0.518 | 1.818 |  |  |  | 3465 | 555 | 22.128 |  | 0.253
| 2019-06-15 19:30 | 133 | 1596 | 1.596 | 10.085 | 22.138 | 22.908 | 1.422 | 0.524 | 1.824 |  |  |  | 3480 | 570 | 22.138 |  | 0.259
| 2019-06-15 19:45 | 134 | 1608 | 1.608 | 10.116 | 22.151 | 22.921 | 1.412 | 0.534 | 1.834 |  |  |  | 3495 | 585 | 22.151 |  | 0.269
| 2019-06-15 20:00 | 133 | 1596 | 1.596 | 10.098 | 22.152 | 22.922 | 1.418 | 0.528 | 1.828 |  |  |  | 3510 | 600 | 22.152 |  | 0.263
| 2019-06-15 20:15 | 134 | 1608 | 1.608 | 10.11 | 22.168 | 22.938 | 1.424 | 0.522 | 1.822 |  |  |  | 3525 | 615 | 22.168 |  | 0.257
| 2019-06-15 20:30 | 134 | 1608 | 1.608 | 10.091 | 22.182 | 22.952 | 1.429 | 0.517 | 1.817 |  |  |  | 3540 | 630 | 22.182 |  | 0.252
| 2019-06-15 20:45 | 133 | 1596 | 1.596 | 10.095 | 22.168 | 22.938 | 1.422 | 0.524 | 1.824 |  |  |  | 3555 | 645 | 22.168 |  | 0.259
| 2019-06-15 21:00 | 133 | 1596 | 1.596 | 10.088 | 22.188 | 22.958 | 1.421 | 0.525 | 1.825 |  |  |  | 3570 | 660 | 22.188 |  | 0.26
| 2019-06-15 21:15 | 133 | 1596 | 1.596 | 10.085 | 22.201 | 22.971 | 1.43 | 0.516 | 1.816 |  |  |  | 3585 | 675 | 22.201 |  | 0.251
| 2019-06-15 21:30 | 133 | 1596 | 1.596 | 10.09 | 22.207 | 22.977 | 1.422 | 0.524 | 1.824 |  |  |  | 3600 | 690 | 22.207 |  | 0.259
| 2019-06-15 21:45 | 133 | 1596 | 1.596 | 10.106 | 22.21 | 22.98 | 1.421 | 0.525 | 1.825 |  |  |  | 3615 | 705 | 22.21 |  | 0.26
| 2019-06-15 22:00 | 133 | 1596 | 1.596 | 10.117 | 22.223 | 22.993 | 1.418 | 0.528 | 1.828 |  |  |  | 3630 | 720 | 22.223 |  | 0.263
| 2019-06-15 22:15 | 133 | 1596 | 1.596 | 10.096 | 22.238 | 23.008 | 1.431 | 0.515 | 1.815 |  |  |  | 3645 | 735 | 22.238 |  | 0.25
| 2019-06-15 22:30 | 133 | 1596 | 1.596 | 10.08 | 22.255 | 23.025 | 1.423 | 0.523 | 1.823 |  |  |  | 3660 | 750 | 22.255 |  | 0.258
| 2019-06-15 22:45 | 134 | 1608 | 1.608 | 10.082 | 22.299 | 23.069 | 1.427 | 0.519 | 1.819 |  |  |  | 3675 | 765 | 22.299 |  | 0.254
| 2019-06-15 23:00 | 131 | 1572 | 1.572 | 10.088 | 22.278 | 23.048 | 1.426 | 0.52 | 1.82 |  |  |  | 3690 | 780 | 22.278 |  | 0.255
| 2019-06-15 23:15 | 132 | 1584 | 1.584 | 10.114 | 22.247 | 23.017 | 1.43 | 0.516 | 1.816 |  |  |  | 3705 | 795 | 22.247 |  | 0.251
| 2019-06-15 23:30 | 133 | 1596 | 1.596 | 10.097 | 22.208 | 22.978 | 1.427 | 0.519 | 1.819 |  |  |  | 3720 | 810 | 22.208 |  | 0.254
| 2019-06-15 23:45 | 132 | 1584 | 1.584 | 10.109 | 22.197 | 22.967 | 1.434 | 0.512 | 1.812 |  |  |  | 3735 | 825 | 22.197 |  | 0.247
| 2019-06-16 | 132 | 1584 | 1.584 | 10.097 | 22.2 | 22.97 | 1.422 | 0.524 | 1.824 |  |  |  | 3750 | 840 | 22.2 |  | 0.259
| 2019-06-16 00:15 | 132 | 1584 | 1.584 | 10.093 | 22.184 | 22.954 | 1.422 | 0.524 | 1.824 |  |  |  | 3765 | 855 | 22.184 |  | 0.259
| 2019-06-16 00:30 | 132 | 1584 | 1.584 | 10.103 | 22.192 | 22.962 | 1.433 | 0.513 | 1.813 |  |  |  | 3780 | 870 | 22.192 |  | 0.248
| 2019-06-16 00:45 | 132 | 1584 | 1.584 | 10.103 | 22.195 | 22.965 | 1.43 | 0.516 | 1.816 |  |  |  | 3795 | 885 | 22.195 |  | 0.251
| 2019-06-16 01:00 | 132 | 1584 | 1.584 | 10.081 | 22.195 | 22.965 | 1.429 | 0.517 | 1.817 |  |  |  | 3810 | 900 | 22.195 |  | 0.252
| 2019-06-16 01:15 | 133 | 1596 | 1.596 | 10.085 | 22.211 | 22.981 | 1.42 | 0.526 | 1.826 |  |  |  | 3825 | 915 | 22.211 |  | 0.261
| 2019-06-16 01:30 | 133 | 1596 | 1.596 | 10.088 | 22.21 | 22.98 | 1.418 | 0.528 | 1.828 |  |  |  | 3840 | 930 | 22.21 |  | 0.263
| 2019-06-16 01:45 | 132 | 1584 | 1.584 | 10.097 | 22.204 | 22.974 | 1.438 | 0.508 | 1.808 |  |  |  | 3855 | 945 | 22.204 |  | 0.243
| 2019-06-16 02:00 | 132 | 1584 | 1.584 | 10.09 | 22.209 | 22.979 | 1.437 | 0.509 | 1.809 |  |  |  | 3870 | 960 | 22.209 |  | 0.244
| 2019-06-16 02:15 | 132 | 1584 | 1.584 | 10.099 | 22.184 | 22.954 | 1.435 | 0.511 | 1.811 |  |  |  | 3885 | 975 | 22.184 |  | 0.246
| 2019-06-16 02:30 | 132 | 1584 | 1.584 | 10.092 | 22.179 | 22.949 | 1.434 | 0.512 | 1.812 |  |  |  | 3900 | 990 | 22.179 |  | 0.247
| 2019-06-16 02:45 | 132 | 1584 | 1.584 | 10.094 | 22.195 | 22.965 | 1.439 | 0.507 | 1.807 |  |  |  | 3915 | 1005 | 22.195 |  | 0.242
| 2019-06-16 03:00 | 132 | 1584 | 1.584 | 10.099 | 22.179 | 22.949 | 1.442 | 0.504 | 1.804 |  |  |  | 3930 | 1020 | 22.179 |  | 0.239
| 2019-06-16 03:15 | 132 | 1584 | 1.584 | 10.081 | 22.192 | 22.962 | 1.428 | 0.518 | 1.818 |  |  |  | 3945 | 1035 | 22.192 |  | 0.253
| 2019-06-16 03:30 | 133 | 1596 | 1.596 | 10.094 | 22.205 | 22.975 | 1.431 | 0.515 | 1.815 |  |  |  | 3960 | 1050 | 22.205 |  | 0.25
| 2019-06-16 03:45 | 132 | 1584 | 1.584 | 10.097 | 22.227 | 22.997 | 1.421 | 0.525 | 1.825 |  |  |  | 3975 | 1065 | 22.227 |  | 0.26
| 2019-06-16 04:00 | 132 | 1584 | 1.584 | 10.096 | 22.208 | 22.978 | 1.431 | 0.515 | 1.815 |  |  |  | 3990 | 1080 | 22.208 |  | 0.25
| 2019-06-16 04:15 | 132 | 1584 | 1.584 | 10.109 | 22.202 | 22.972 | 1.431 | 0.515 | 1.815 |  |  |  | 4005 | 1095 | 22.202 |  | 0.25
| 2019-06-16 04:30 | 133 | 1596 | 1.596 | 10.102 | 22.213 | 22.983 | 1.443 | 0.503 | 1.803 |  |  |  | 4020 | 1110 | 22.213 |  | 0.238
| 2019-06-16 04:45 | 132 | 1584 | 1.584 | 10.104 | 22.212 | 22.982 | 1.43 | 0.516 | 1.816 |  |  |  | 4035 | 1125 | 22.212 |  | 0.251
| 2019-06-16 05:00 | 132 | 1584 | 1.584 | 10.097 | 22.237 | 23.007 | 1.431 | 0.515 | 1.815 |  |  |  | 4050 | 1140 | 22.237 |  | 0.25
| 2019-06-16 05:15 | 132 | 1584 | 1.584 | 10.102 | 22.226 | 22.996 | 1.429 | 0.517 | 1.817 |  |  |  | 4065 | 1155 | 22.226 |  | 0.252
| 2019-06-16 05:30 | 133 | 1596 | 1.596 | 10.097 | 22.273 | 23.043 | 1.436 | 0.51 | 1.81 |  |  |  | 4080 | 1170 | 22.273 |  | 0.245
| 2019-06-16 05:45 | 132 | 1584 | 1.584 | 10.095 | 22.302 | 23.072 | 1.436 | 0.51 | 1.81 |  |  |  | 4095 | 1185 | 22.302 |  | 0.245
| 2019-06-16 06:00 | 132 | 1584 | 1.584 | 10.108 | 22.314 | 23.084 | 1.428 | 0.518 | 1.818 |  |  |  | 4110 | 1200 | 22.314 |  | 0.253
| 2019-06-16 06:15 | 132 | 1584 | 1.584 | 10.065 | 22.302 | 23.072 | 1.448 | 0.498 | 1.798 |  |  |  | 4125 | 1215 | 22.302 |  | 0.233
| 2019-06-16 06:30 | 133 | 1596 | 1.596 | 10.092 | 22.323 | 23.093 | 1.432 | 0.514 | 1.814 |  |  |  | 4140 | 1230 | 22.323 |  | 0.249
| 2019-06-16 06:45 | 133 | 1596 | 1.596 | 10.102 | 22.307 | 23.077 | 1.443 | 0.503 | 1.803 |  |  |  | 4155 | 1245 | 22.307 |  | 0.238
| 2019-06-16 07:00 | 132 | 1584 | 1.584 | 10.093 | 22.335 | 23.105 | 1.45 | 0.496 | 1.796 |  |  |  | 4170 | 1260 | 22.335 |  | 0.231
| 2019-06-16 07:15 | 133 | 1596 | 1.596 | 10.097 | 22.349 | 23.119 | 1.443 | 0.503 | 1.803 |  |  |  | 4185 | 1275 | 22.349 |  | 0.238
| 2019-06-16 07:30 | 133 | 1596 | 1.596 | 10.104 | 22.371 | 23.141 | 1.44 | 0.506 | 1.806 |  |  |  | 4200 | 1290 | 22.371 |  | 0.241
| 2019-06-16 07:45 | 133 | 1596 | 1.596 | 10.088 | 22.391 | 23.161 | 1.441 | 0.505 | 1.805 |  |  |  | 4215 | 1305 | 22.391 |  | 0.24
| 2019-06-16 08:00 | 132 | 1584 | 1.584 | 10.103 | 22.371 | 23.141 | 1.444 | 0.502 | 1.802 |  |  |  | 4230 | 1320 | 22.371 |  | 0.237
| 2019-06-16 08:15 | 133 | 1596 | 1.596 | 10.088 | 22.391 | 23.161 | 1.436 | 0.51 | 1.81 |  |  |  | 4245 | 1335 | 22.391 |  | 0.245
| 2019-06-16 08:30 | 132 | 1584 | 1.584 | 10.094 | 22.403 | 23.173 | 1.445 | 0.501 | 1.801 |  |  |  | 4260 | 1350 | 22.403 |  | 0.236
| 2019-06-16 08:45 | 133 | 1596 | 1.596 | 10.082 | 22.377 | 23.147 | 1.444 | 0.502 | 1.802 |  |  |  | 4275 | 1365 | 22.377 |  | 0.237
| 2019-06-16 09:00 | 132 | 1584 | 1.584 | 10.111 | 22.397 | 23.167 | 1.434 | 0.512 | 1.812 | 0.24 |  |  | 4290 | 1380 | 22.397 |  | 0.247
| 2019-06-16 09:15 | 132 | 1584 | 1.584 | 10.091 | 22.401 | 23.171 | 1.444 | 0.502 | 1.802 |  |  |  | 4305 | 1395 | 22.401 |  | 0.237
| 2019-06-16 09:30 | 133 | 1596 | 1.596 | 10.1 | 22.392 | 23.162 | 1.445 | 0.501 | 1.801 |  |  |  | 4320 | 1410 | 22.392 |  | 0.236
| 2019-06-16 09:45 | 132 | 1584 | 1.584 | 10.097 | 22.381 | 23.151 | 1.442 | 0.504 | 1.804 |  |  |  | 4335 | 1425 | 22.381 |  | 0.239
| 2019-06-16 10:00 | 132 | 1584 | 1.584 | 10.097 | 22.383 | 23.153 | 1.446 | 0.5 | 1.8 |  |  |  | 4350 | 1440 | 22.383 |  | 0.235
| 2019-06-16 10:15 | 132 | 1584 | 1.584 | 10.108 | 22.39 | 23.16 | 1.449 | 0.497 | 1.797 |  |  |  | 4365 | 1455 | 22.39 |  | 0.232
| 2019-06-16 10:30 | 133 | 1596 | 1.596 | 10.091 | 22.385 | 23.155 | 1.448 | 0.498 | 1.798 |  |  |  | 4380 | 1470 | 22.385 |  | 0.233
| 2019-06-16 10:45 | 133 | 1596 | 1.596 | 10.075 | 22.406 | 23.176 | 1.449 | 0.497 | 1.797 |  |  |  | 4395 | 1485 | 22.406 |  | 0.232
| 2019-06-16 11:00 | 132 | 1584 | 1.584 | 10.082 | 22.401 | 23.171 | 1.455 | 0.491 | 1.791 |  |  |  | 4410 | 1500 | 22.401 |  | 0.226
| 2019-06-16 11:15 | 133 | 1596 | 1.596 | 10.093 | 22.425 | 23.195 | 1.44 | 0.506 | 1.806 |  |  |  | 4425 | 1515 | 22.425 |  | 0.241
| 2019-06-16 11:30 | 132 | 1584 | 1.584 | 10.093 | 22.401 | 23.171 | 1.455 | 0.491 | 1.791 |  |  |  | 4440 | 1530 | 22.401 |  | 0.226
| 2019-06-16 11:45 | 132 | 1584 | 1.584 | 10.101 | 22.419 | 23.189 | 1.45 | 0.496 | 1.796 |  |  |  | 4455 | 1545 | 22.419 |  | 0.231
| 2019-06-16 12:00 | 132 | 1584 | 1.584 | 10.088 | 22.409 | 23.179 | 1.451 | 0.495 | 1.795 |  |  |  | 4470 | 1560 | 22.409 |  | 0.23
| 2019-06-16 12:15 | 132 | 1584 | 1.584 | 10.093 | 22.413 | 23.183 | 1.448 | 0.498 | 1.798 |  |  |  | 4485 | 1575 | 22.413 |  | 0.233
| 2019-06-16 12:30 | 132 | 1584 | 1.584 | 10.094 | 22.407 | 23.177 | 1.45 | 0.496 | 1.796 |  |  |  | 4500 | 1590 | 22.407 |  | 0.231
| 2019-06-16 12:45 | 132 | 1584 | 1.584 | 10.085 | 22.417 | 23.187 | 1.452 | 0.494 | 1.794 |  |  |  | 4515 | 1605 | 22.417 |  | 0.229
| 2019-06-16 13:00 | 132 | 1584 | 1.584 | 10.084 | 22.405 | 23.175 | 1.453 | 0.493 | 1.793 |  |  |  | 4530 | 1620 | 22.405 |  | 0.228
| 2019-06-16 13:15 | 133 | 1596 | 1.596 | 10.104 | 22.414 | 23.184 | 1.461 | 0.485 | 1.785 |  |  |  | 4545 | 1635 | 22.414 |  | 0.22
| 2019-06-16 13:30 | 132 | 1584 | 1.584 | 10.082 | 22.421 | 23.191 | 1.451 | 0.495 | 1.795 |  |  |  | 4560 | 1650 | 22.421 |  | 0.23
| 2019-06-16 13:45 | 132 | 1584 | 1.584 | 10.091 | 22.422 | 23.192 | 1.452 | 0.494 | 1.794 |  |  |  | 4575 | 1665 | 22.422 |  | 0.229
| 2019-06-16 14:00 | 133 | 1596 | 1.596 | 10.096 | 22.418 | 23.188 | 1.464 | 0.482 | 1.782 |  |  |  | 4590 | 1680 | 22.418 |  | 0.217
| 2019-06-16 14:15 | 133 | 1596 | 1.596 | 10.08 | 22.433 | 23.203 | 1.453 | 0.493 | 1.793 |  |  |  | 4605 | 1695 | 22.433 |  | 0.228
| 2019-06-16 14:30 | 132 | 1584 | 1.584 | 10.098 | 22.44 | 23.21 | 1.466 | 0.48 | 1.78 |  |  |  | 4620 | 1710 | 22.44 |  | 0.215
| 2019-06-16 14:45 | 132 | 1584 | 1.584 | 10.12 | 22.436 | 23.206 | 1.461 | 0.485 | 1.785 |  |  |  | 4635 | 1725 | 22.436 |  | 0.22
| 2019-06-16 15:00 | 133 | 1596 | 1.596 | 10.078 | 22.44 | 23.21 | 1.455 | 0.491 | 1.791 |  |  |  | 4650 | 1740 | 22.44 |  | 0.226
| 2019-06-16 15:15 | 133 | 1596 | 1.596 | 10.08 | 22.456 | 23.226 | 1.45 | 0.496 | 1.796 |  |  |  | 4665 | 1755 | 22.456 |  | 0.231
| 2019-06-16 15:30 | 132 | 1584 | 1.584 | 10.088 | 22.474 | 23.244 | 1.462 | 0.484 | 1.784 |  |  |  | 4680 | 1770 | 22.474 |  | 0.219
| 2019-06-16 15:45 | 133 | 1596 | 1.596 | 10.089 | 22.467 | 23.237 | 1.466 | 0.48 | 1.78 |  |  |  | 4695 | 1785 | 22.467 |  | 0.215
| 2019-06-16 16:00 | 132 | 1584 | 1.584 | 10.106 | 22.472 | 23.242 | 1.458 | 0.488 | 1.788 |  |  |  | 4710 | 1800 | 22.472 |  | 0.223
| 2019-06-16 16:15 | 132 | 1584 | 1.584 | 10.097 | 22.474 | 23.244 | 1.457 | 0.489 | 1.789 |  |  |  | 4725 | 1815 | 22.474 |  | 0.224
| 2019-06-16 16:30 | 132 | 1584 | 1.584 | 10.111 | 22.464 | 23.234 | 1.455 | 0.491 | 1.791 |  |  |  | 4740 | 1830 | 22.464 |  | 0.226
| 2019-06-16 16:45 | 132 | 1584 | 1.584 | 10.088 | 22.475 | 23.245 | 1.455 | 0.491 | 1.791 |  |  |  | 4755 | 1845 | 22.475 |  | 0.226
| 2019-06-16 17:00 | 132 | 1584 | 1.584 | 10.088 | 22.455 | 23.225 | 1.458 | 0.488 | 1.788 |  |  |  | 4770 | 1860 | 22.455 |  | 0.223
| 2019-06-16 17:15 | 132 | 1584 | 1.584 | 10.092 | 22.457 | 23.227 | 1.454 | 0.492 | 1.792 |  |  |  | 4785 | 1875 | 22.457 |  | 0.227
| 2019-06-16 17:30 | 132 | 1584 | 1.584 | 10.107 | 22.433 | 23.203 | 1.456 | 0.49 | 1.79 |  |  |  | 4800 | 1890 | 22.433 |  | 0.225
| 2019-06-16 17:45 | 132 | 1584 | 1.584 | 10.079 | 22.439 | 23.209 | 1.473 | 0.473 | 1.773 |  |  |  | 4815 | 1905 | 22.439 |  | 0.208
| 2019-06-16 18:00 | 132 | 1584 | 1.584 | 10.102 | 22.437 | 23.207 | 1.458 | 0.488 | 1.788 |  |  |  | 4830 | 1920 | 22.437 |  | 0.223
| 2019-06-16 18:15 | 131 | 1572 | 1.572 | 10.114 | 22.433 | 23.203 | 1.464 | 0.482 | 1.782 |  |  |  | 4845 | 1935 | 22.433 |  | 0.217
| 2019-06-16 18:30 | 132 | 1584 | 1.584 | 10.097 | 22.446 | 23.216 | 1.451 | 0.495 | 1.795 |  |  |  | 4860 | 1950 | 22.446 |  | 0.23
| 2019-06-16 18:45 | 132 | 1584 | 1.584 | 10.069 | 22.471 | 23.241 | 1.465 | 0.481 | 1.781 |  |  |  | 4875 | 1965 | 22.471 |  | 0.216
| 2019-06-16 19:00 | 132 | 1584 | 1.584 | 10.101 | 22.483 | 23.253 | 1.461 | 0.485 | 1.785 |  |  |  | 4890 | 1980 | 22.483 |  | 0.22
| 2019-06-16 19:15 | 132 | 1584 | 1.584 | 10.083 | 22.474 | 23.244 | 1.46 | 0.486 | 1.786 |  |  |  | 4905 | 1995 | 22.474 |  | 0.221
| 2019-06-16 19:30 | 133 | 1596 | 1.596 | 10.097 | 22.532 | 23.302 | 1.478 | 0.468 | 1.768 |  |  |  | 4920 | 2010 | 22.532 |  | 0.203
| 2019-06-16 19:45 | 133 | 1596 | 1.596 | 10.092 | 22.528 | 23.298 | 1.461 | 0.485 | 1.785 |  |  |  | 4935 | 2025 | 22.528 |  | 0.22
| 2019-06-16 20:00 | 133 | 1596 | 1.596 | 10.105 | 22.531 | 23.301 | 1.462 | 0.484 | 1.784 |  |  |  | 4950 | 2040 | 22.531 |  | 0.219
| 2019-06-16 20:15 | 133 | 1596 | 1.596 | 10.098 | 22.543 | 23.313 | 1.45 | 0.496 | 1.796 |  |  |  | 4965 | 2055 | 22.543 |  | 0.231
| 2019-06-16 20:30 | 133 | 1596 | 1.596 | 10.103 | 22.555 | 23.325 | 1.46 | 0.486 | 1.786 |  |  |  | 4980 | 2070 | 22.555 |  | 0.221
| 2019-06-16 20:45 | 132 | 1584 | 1.584 | 10.087 | 22.547 | 23.317 | 1.465 | 0.481 | 1.781 |  |  |  | 4995 | 2085 | 22.547 |  | 0.216
| 2019-06-16 21:00 | 132 | 1584 | 1.584 | 10.084 | 22.558 | 23.328 | 1.475 | 0.471 | 1.771 |  |  |  | 5010 | 2100 | 22.558 |  | 0.206
| 2019-06-16 21:15 | 132 | 1584 | 1.584 | 10.108 | 22.554 | 23.324 | 1.46 | 0.486 | 1.786 |  |  |  | 5025 | 2115 | 22.554 |  | 0.221
| 2019-06-16 21:30 | 132 | 1584 | 1.584 | 10.118 | 22.566 | 23.336 | 1.462 | 0.484 | 1.784 |  |  |  | 5040 | 2130 | 22.566 |  | 0.219
| 2019-06-16 21:45 | 132 | 1584 | 1.584 | 10.114 | 22.545 | 23.315 | 1.458 | 0.488 | 1.788 |  |  |  | 5055 | 2145 | 22.545 |  | 0.223
| 2019-06-16 22:00 | 132 | 1584 | 1.584 | 10.087 | 22.543 | 23.313 | 1.462 | 0.484 | 1.784 |  |  |  | 5070 | 2160 | 22.543 |  | 0.219
| 2019-06-16 22:15 | 132 | 1584 | 1.584 | 10.094 | 22.552 | 23.322 | 1.466 | 0.48 | 1.78 |  |  |  | 5085 | 2175 | 22.552 |  | 0.215
| 2019-06-16 22:30 | 132 | 1584 | 1.584 | 10.096 | 22.553 | 23.323 | 1.462 | 0.484 | 1.784 |  |  |  | 5100 | 2190 | 22.553 |  | 0.219
| 2019-06-16 22:45 | 132 | 1584 | 1.584 | 10.1 | 22.567 | 23.337 | 1.469 | 0.477 | 1.777 |  |  |  | 5115 | 2205 | 22.567 |  | 0.212
| 2019-06-16 23:00 | 132 | 1584 | 1.584 | 10.106 | 22.584 | 23.354 | 1.467 | 0.479 | 1.779 |  |  |  | 5130 | 2220 | 22.584 |  | 0.214
| 2019-06-16 23:15 | 132 | 1584 | 1.584 | 10.094 | 22.598 | 23.368 | 1.459 | 0.487 | 1.787 |  |  |  | 5145 | 2235 | 22.598 |  | 0.222
| 2019-06-16 23:30 | 133 | 1596 | 1.596 | 10.1 | 22.58 | 23.35 | 1.461 | 0.485 | 1.785 |  |  |  | 5160 | 2250 | 22.58 |  | 0.22
| 2019-06-16 23:45 | 132 | 1584 | 1.584 | 10.082 | 22.604 | 23.374 | 1.458 | 0.488 | 1.788 |  |  |  | 5175 | 2265 | 22.604 |  | 0.223
| 2019-06-17 | 132 | 1584 | 1.584 | 10.074 | 22.595 | 23.365 | 1.46 | 0.486 | 1.786 |  |  |  | 5190 | 2280 | 22.595 |  | 0.221
| 2019-06-17 00:15 | 132 | 1584 | 1.584 | 10.094 | 22.585 | 23.355 | 1.467 | 0.479 | 1.779 |  |  |  | 5205 | 2295 | 22.585 |  | 0.214
| 2019-06-17 00:30 | 132 | 1584 | 1.584 | 10.086 | 22.579 | 23.349 | 1.465 | 0.481 | 1.781 |  |  |  | 5220 | 2310 | 22.579 |  | 0.216
| 2019-06-17 00:45 | 132 | 1584 | 1.584 | 10.086 | 22.594 | 23.364 | 1.469 | 0.477 | 1.777 |  |  |  | 5235 | 2325 | 22.594 |  | 0.212
| 2019-06-17 01:00 | 132 | 1584 | 1.584 | 10.108 | 22.585 | 23.355 | 1.465 | 0.481 | 1.781 |  |  |  | 5250 | 2340 | 22.585 |  | 0.216
| 2019-06-17 01:15 | 132 | 1584 | 1.584 | 10.098 | 22.562 | 23.332 | 1.463 | 0.483 | 1.783 |  |  |  | 5265 | 2355 | 22.562 |  | 0.218
| 2019-06-17 01:30 | 132 | 1584 | 1.584 | 10.1 | 22.567 | 23.337 | 1.455 | 0.491 | 1.791 |  |  |  | 5280 | 2370 | 22.567 |  | 0.226
| 2019-06-17 01:45 | 132 | 1584 | 1.584 | 10.098 | 22.566 | 23.336 | 1.457 | 0.489 | 1.789 |  |  |  | 5295 | 2385 | 22.566 |  | 0.224
| 2019-06-17 02:00 | 131 | 1572 | 1.572 | 10.086 | 22.524 | 23.294 | 1.454 | 0.492 | 1.792 |  |  |  | 5310 | 2400 | 22.524 |  | 0.227
| 2019-06-17 02:15 | 132 | 1584 | 1.584 | 10.102 | 22.534 | 23.304 | 1.457 | 0.489 | 1.789 |  |  |  | 5325 | 2415 | 22.534 |  | 0.224
| 2019-06-17 02:30 | 132 | 1584 | 1.584 | 10.094 | 22.54 | 23.31 | 1.463 | 0.483 | 1.783 |  |  |  | 5340 | 2430 | 22.54 |  | 0.218
| 2019-06-17 02:45 | 132 | 1584 | 1.584 | 10.09 | 22.542 | 23.312 | 1.451 | 0.495 | 1.795 |  |  |  | 5355 | 2445 | 22.542 |  | 0.23
| 2019-06-17 03:00 | 132 | 1584 | 1.584 | 10.087 | 22.528 | 23.298 | 1.449 | 0.497 | 1.797 |  |  |  | 5370 | 2460 | 22.528 |  | 0.232
| 2019-06-17 03:15 | 132 | 1584 | 1.584 | 10.1 | 22.529 | 23.299 | 1.45 | 0.496 | 1.796 |  |  |  | 5385 | 2475 | 22.529 |  | 0.231
| 2019-06-17 03:30 | 132 | 1584 | 1.584 | 10.095 | 22.524 | 23.294 | 1.448 | 0.498 | 1.798 |  |  |  | 5400 | 2490 | 22.524 |  | 0.233
| 2019-06-17 03:45 | 132 | 1584 | 1.584 | 10.108 | 22.539 | 23.309 | 1.467 | 0.479 | 1.779 |  |  |  | 5415 | 2505 | 22.539 |  | 0.214
| 2019-06-17 04:00 | 132 | 1584 | 1.584 | 10.088 | 22.54 | 23.31 | 1.463 | 0.483 | 1.783 |  |  |  | 5430 | 2520 | 22.54 |  | 0.218
| 2019-06-17 04:15 | 131 | 1572 | 1.572 | 10.103 | 22.532 | 23.302 | 1.464 | 0.482 | 1.782 |  |  |  | 5445 | 2535 | 22.532 |  | 0.217
| 2019-06-17 04:30 | 132 | 1584 | 1.584 | 10.081 | 22.532 | 23.302 | 1.465 | 0.481 | 1.781 |  |  |  | 5460 | 2550 | 22.532 |  | 0.216
| 2019-06-17 04:45 | 132 | 1584 | 1.584 | 10.076 | 22.553 | 23.323 | 1.459 | 0.487 | 1.787 |  |  |  | 5475 | 2565 | 22.553 |  | 0.222
| 2019-06-17 05:00 | 131 | 1572 | 1.572 | 10.076 | 22.55 | 23.32 | 1.461 | 0.485 | 1.785 |  |  |  | 5490 | 2580 | 22.55 |  | 0.22
| 2019-06-17 05:15 | 133 | 1596 | 1.596 | 10.085 | 22.56 | 23.33 | 1.46 | 0.486 | 1.786 |  |  |  | 5505 | 2595 | 22.56 |  | 0.221
| 2019-06-17 05:30 | 132 | 1584 | 1.584 | 10.086 | 22.582 | 23.352 | 1.466 | 0.48 | 1.78 |  |  |  | 5520 | 2610 | 22.582 |  | 0.215
| 2019-06-17 05:45 | 132 | 1584 | 1.584 | 10.101 | 22.567 | 23.337 | 1.458 | 0.488 | 1.788 |  |  |  | 5535 | 2625 | 22.567 |  | 0.223
| 2019-06-17 06:00 | 132 | 1584 | 1.584 | 10.095 | 22.571 | 23.341 | 1.457 | 0.489 | 1.789 |  |  |  | 5550 | 2640 | 22.571 |  | 0.224
| 2019-06-17 06:15 | 132 | 1584 | 1.584 | 10.102 | 22.573 | 23.343 | 1.464 | 0.482 | 1.782 |  |  |  | 5565 | 2655 | 22.573 |  | 0.217
| 2019-06-17 06:30 | 132 | 1584 | 1.584 | 10.083 | 22.569 | 23.339 | 1.473 | 0.473 | 1.773 |  |  |  | 5580 | 2670 | 22.569 |  | 0.208
| 2019-06-17 06:45 | 131 | 1572 | 1.572 | 10.097 | 22.566 | 23.336 | 1.462 | 0.484 | 1.784 |  |  |  | 5595 | 2685 | 22.566 |  | 0.219
| 2019-06-17 07:00 | 132 | 1584 | 1.584 | 10.103 | 22.562 | 23.332 | 1.47 | 0.476 | 1.776 |  |  |  | 5610 | 2700 | 22.562 |  | 0.211
| 2019-06-17 07:15 | 132 | 1584 | 1.584 | 10.094 | 22.557 | 23.327 | 1.462 | 0.484 | 1.784 |  |  |  | 5625 | 2715 | 22.557 |  | 0.219
| 2019-06-17 07:30 | 131 | 1572 | 1.572 | 10.088 | 22.525 | 23.295 | 1.475 | 0.471 | 1.771 |  |  |  | 5640 | 2730 | 22.525 |  | 0.206
| 2019-06-17 07:45 | 132 | 1584 | 1.584 | 10.068 | 22.514 | 23.284 | 1.462 | 0.484 | 1.784 |  |  |  | 5655 | 2745 | 22.514 |  | 0.219
| 2019-06-17 08:00 | 132 | 1584 | 1.584 | 10.094 | 22.503 | 23.273 | 1.46 | 0.486 | 1.786 |  |  |  | 5670 | 2760 | 22.503 |  | 0.221
| 2019-06-17 08:15 | 130 | 1560 | 1.56 | 10.1 | 22.534 | 23.304 | 1.655 | 0.291 | 1.591 |  |  |  | 5685 | 2775 | 22.534 |  | 0.026
Recovery test - pump turned off | 2019-06-17 08:30 | 0 | 0 | 0 | 10.092 | 22.73 | 23.5 | 1.68 | 0.266 | 1.566 |  |  |  | 5700 | 0 | 22.73 |  | 0.001
| 2019-06-17 08:45 | 0 | 0 | 0 | 10.098 | 16.466 | 17.236 | 1.712 | 0.234 | 1.534 |  |  |  | 5715 | 15 | 16.466 | 381 | -0.031
| 2019-06-17 09:00 | 0 | 0 | 0 | 10.108 | 12.362 | 13.132 | 1.708 | 0.238 | 1.538 | 0.29 | 1.55 | 22.77 | 5730 | 30 | 12.362 | 191 | -0.027
| 2019-06-17 09:15 | 0 | 0 | 0 | 10.092 | 9.259 | 10.029 | 1.72 | 0.226 | 1.526 |  |  |  | 5745 | 45 | 9.259 | 127.6667 | -0.039
| 2019-06-17 09:30 | 0 | 0 | 0 | 10.094 | 6.991 | 7.761 | 1.718 | 0.228 | 1.528 |  |  |  | 5760 | 60 | 6.991 | 96 | -0.037
| 2019-06-17 09:45 | 0 | 0 | 0 | 10.099 | 5.09 | 5.86 | 1.723 | 0.223 | 1.523 |  |  |  | 5775 | 75 | 5.09 | 77 | -0.042
| 2019-06-17 10:00 | 0 | 0 | 0 | 10.1 | 3.831 | 4.601 | 1.711 | 0.235 | 1.535 |  |  |  | 5790 | 90 | 3.831 | 64.3333 | -0.03
| 2019-06-17 10:15 | 0 | 0 | 0 | 10.092 | 2.999 | 3.769 | 1.73 | 0.216 | 1.516 |  |  |  | 5805 | 105 | 2.999 | 55.2857 | -0.049
| 2019-06-17 10:30 | 0 | 0 | 0 | 10.103 | 2.42 | 3.19 | 1.709 | 0.237 | 1.537 |  |  |  | 5820 | 120 | 2.42 | 48.5 | -0.028
| 2019-06-17 10:45 | 0 | 0 | 0 | 10.1 | 1.989 | 2.759 | 1.727 | 0.219 | 1.519 |  |  |  | 5835 | 135 | 1.989 | 43.2222 | -0.046
| 2019-06-17 11:00 | 0 | 0 | 0 | 10.11 | 1.72 | 2.49 | 1.73 | 0.216 | 1.516 |  |  |  | 5850 | 150 | 1.72 | 39 | -0.049
| 2019-06-17 11:15 | 0 | 0 | 0 | 10.108 | 1.492 | 2.262 | 1.718 | 0.228 | 1.528 |  |  |  | 5865 | 165 | 1.492 | 35.5455 | -0.037
| 2019-06-17 11:30 | 0 | 0 | 0 | 10.103 | 1.32 | 2.09 | 1.729 | 0.217 | 1.517 |  |  |  | 5880 | 180 | 1.32 | 32.6667 | -0.048
| 2019-06-17 11:45 | 0 | 0 | 0 | 10.11 | 1.18 | 1.95 | 1.736 | 0.21 | 1.51 |  |  |  | 5895 | 195 | 1.18 | 30.2308 | -0.055
| 2019-06-17 12:00 | 0 | 0 | 0 | 10.109 | 1.048 | 1.818 | 1.723 | 0.223 | 1.523 |  |  |  | 5910 | 210 | 1.048 | 28.1429 | -0.042
| 2019-06-17 12:15 | 0 | 0 | 0 | 10.094 | 0.945 | 1.715 | 1.735 | 0.211 | 1.511 |  |  |  | 5925 | 225 | 0.945 | 26.3333 | -0.054
| 2019-06-17 12:30 | 0 | 0 | 0 | 10.089 | 0.849 | 1.619 | 1.727 | 0.219 | 1.519 |  |  |  | 5940 | 240 | 0.849 | 24.75 | -0.046
| 2019-06-17 12:45 | 0 | 0 | 0 | 10.107 | 0.791 | 1.561 | 1.735 | 0.211 | 1.511 |  |  |  | 5955 | 255 | 0.791 | 23.3529 | -0.054
| 2019-06-17 13:00 | 0 | 0 | 0 | 10.094 | 0.714 | 1.484 | 1.728 | 0.218 | 1.518 |  |  |  | 5970 | 270 | 0.714 | 22.1111 | -0.047
| 2019-06-17 13:15 | 0 | 0 | 0 | 10.086 | 0.671 | 1.441 | 1.731 | 0.215 | 1.515 |  |  |  | 5985 | 285 | 0.671 | 21 | -0.05
| 2019-06-17 13:30 | 0 | 0 | 0 | 10.085 | 0.64 | 1.41 | 1.743 | 0.203 | 1.503 |  |  |  | 6000 | 300 | 0.64 | 20 | -0.062
| 2019-06-17 13:45 | 0 | 0 | 0 | 10.078 | 0.6 | 1.37 | 1.727 | 0.219 | 1.519 |  |  |  | 6015 | 315 | 0.6 | 19.0952 | -0.046
| 2019-06-17 14:00 | 0 | 0 | 0 | 10.086 | 0.556 | 1.326 | 1.719 | 0.227 | 1.527 |  |  |  | 6030 | 330 | 0.556 | 18.2727 | -0.038
| 2019-06-17 14:15 | 0 | 0 | 0 | 10.09 | 0.51 | 1.28 | 1.721 | 0.225 | 1.525 |  |  |  | 6045 | 345 | 0.51 | 17.5217 | -0.04
| 2019-06-17 14:30 | 0 | 0 | 0 | 10.102 | 0.493 | 1.263 | 1.735 | 0.211 | 1.511 |  |  |  | 6060 | 360 | 0.493 | 16.8333 | -0.054
| 2019-06-17 14:45 | 0 | 0 | 0 | 10.088 | 0.471 | 1.241 | 1.742 | 0.204 | 1.504 |  |  |  | 6075 | 375 | 0.471 | 16.2 | -0.061
| 2019-06-17 15:00 | 0 | 0 | 0 | 10.103 | 0.454 | 1.224 | 1.739 | 0.207 | 1.507 |  |  |  | 6090 | 390 | 0.454 | 15.6154 | -0.058
| 2019-06-17 15:15 | 0 | 0 | 0 | 10.092 | 0.424 | 1.194 | 1.738 | 0.208 | 1.508 |  |  |  | 6105 | 405 | 0.424 | 15.0741 | -0.057
| 2019-06-17 15:30 | 0 | 0 | 0 | 10.086 | 0.406 | 1.176 | 1.734 | 0.212 | 1.512 |  |  |  | 6120 | 420 | 0.406 | 14.5714 | -0.053
| 2019-06-17 15:45 | 0 | 0 | 0 | 10.069 | 0.39 | 1.16 | 1.725 | 0.221 | 1.521 |  |  |  | 6135 | 435 | 0.39 | 14.1034 | -0.044
| 2019-06-17 16:00 | 0 | 0 | 0 | 10.078 | 0.365 | 1.135 | 1.738 | 0.208 | 1.508 |  |  |  | 6150 | 450 | 0.365 | 13.6667 | -0.057
| 2019-06-17 16:15 | 0 | 0 | 0 | 10.097 | 0.364 | 1.134 | 1.742 | 0.204 | 1.504 |  |  |  | 6165 | 465 | 0.364 | 13.2581 | -0.061
| 2019-06-17 16:30 | 0 | 0 | 0 | 10.085 | 0.341 | 1.111 | 1.737 | 0.209 | 1.509 |  |  |  | 6180 | 480 | 0.341 | 12.875 | -0.056
| 2019-06-17 16:45 | 0 | 0 | 0 | 10.106 | 0.329 | 1.099 | 1.752 | 0.194 | 1.494 |  |  |  | 6195 | 495 | 0.329 | 12.5152 | -0.071
| 2019-06-17 17:00 | 0 | 0 | 0 | 10.094 | 0.331 | 1.101 | 1.744 | 0.202 | 1.502 |  |  |  | 6210 | 510 | 0.331 | 12.1765 | -0.063
| 2019-06-17 17:15 | 0 | 0 | 0 | 10.107 | 0.305 | 1.075 | 1.742 | 0.204 | 1.504 |  |  |  | 6225 | 525 | 0.305 | 11.8571 | -0.061
| 2019-06-17 17:30 | 0 | 0 | 0 | 10.099 | 0.303 | 1.073 | 1.742 | 0.204 | 1.504 |  |  |  | 6240 | 540 | 0.303 | 11.5556 | -0.061
| 2019-06-17 17:45 | 0 | 0 | 0 | 10.102 | 0.281 | 1.051 | 1.737 | 0.209 | 1.509 |  |  |  | 6255 | 555 | 0.281 | 11.2703 | -0.056
| 2019-06-17 18:00 | 0 | 0 | 0 | 10.085 | 0.28 | 1.05 | 1.731 | 0.215 | 1.515 |  |  |  | 6270 | 570 | 0.28 | 11 | -0.05
| 2019-06-17 18:15 | 0 | 0 | 0 | 10.109 | 0.281 | 1.051 | 1.743 | 0.203 | 1.503 |  |  |  | 6285 | 585 | 0.281 | 10.7436 | -0.062
| 2019-06-17 18:30 | 0 | 0 | 0 | 10.097 | 0.267 | 1.037 | 1.749 | 0.197 | 1.497 |  |  |  | 6300 | 600 | 0.267 | 10.5 | -0.068
| 2019-06-17 18:45 | 0 | 0 | 0 | 10.091 | 0.253 | 1.023 | 1.755 | 0.191 | 1.491 |  |  |  | 6315 | 615 | 0.253 | 10.2683 | -0.074
| 2019-06-17 19:00 | 0 | 0 | 0 | 10.119 | 0.256 | 1.026 | 1.741 | 0.205 | 1.505 |  |  |  | 6330 | 630 | 0.256 | 10.0476 | -0.06
| 2019-06-17 19:15 | 0 | 0 | 0 | 10.075 | 0.228 | 0.998 | 1.747 | 0.199 | 1.499 |  |  |  | 6345 | 645 | 0.228 | 9.8372 | -0.066
| 2019-06-17 19:30 | 0 | 0 | 0 | 10.098 | 0.234 | 1.004 | 1.737 | 0.209 | 1.509 |  |  |  | 6360 | 660 | 0.234 | 9.6364 | -0.056
| 2019-06-17 19:45 | 0 | 0 | 0 | 10.088 | 0.244 | 1.014 | 1.756 | 0.19 | 1.49 |  |  |  | 6375 | 675 | 0.244 | 9.4444 | -0.075
| 2019-06-17 20:00 | 0 | 0 | 0 | 10.091 | 0.243 | 1.013 | 1.755 | 0.191 | 1.491 |  |  |  | 6390 | 690 | 0.243 | 9.2609 | -0.074
| 2019-06-17 20:15 | 0 | 0 | 0 | 10.102 | 0.231 | 1.001 | 1.752 | 0.194 | 1.494 |  |  |  | 6405 | 705 | 0.231 | 9.0851 | -0.071
| 2019-06-17 20:30 | 0 | 0 | 0 | 10.103 | 0.228 | 0.998 | 1.763 | 0.183 | 1.483 |  |  |  | 6420 | 720 | 0.228 | 8.9167 | -0.082
| 2019-06-17 20:45 | 0 | 0 | 0 | 10.093 | 0.215 | 0.985 | 1.743 | 0.203 | 1.503 |  |  |  | 6435 | 735 | 0.215 | 8.7551 | -0.062
| 2019-06-17 21:00 | 0 | 0 | 0 | 10.083 | 0.213 | 0.983 | 1.755 | 0.191 | 1.491 |  |  |  | 6450 | 750 | 0.213 | 8.6 | -0.074
| 2019-06-17 21:15 | 0 | 0 | 0 | 10.072 | 0.206 | 0.976 | 1.746 | 0.2 | 1.5 |  |  |  | 6465 | 765 | 0.206 | 8.451 | -0.065
| 2019-06-17 21:30 | 0 | 0 | 0 | 10.114 | 0.208 | 0.978 | 1.754 | 0.192 | 1.492 |  |  |  | 6480 | 780 | 0.208 | 8.3077 | -0.073
| 2019-06-17 21:45 | 0 | 0 | 0 | 10.099 | 0.212 | 0.982 | 1.745 | 0.201 | 1.501 |  |  |  | 6495 | 795 | 0.212 | 8.1698 | -0.064
| 2019-06-17 22:00 | 0 | 0 | 0 | 10.083 | 0.213 | 0.983 | 1.743 | 0.203 | 1.503 |  |  |  | 6510 | 810 | 0.213 | 8.037 | -0.062
| 2019-06-17 22:15 | 0 | 0 | 0 | 10.085 | 0.213 | 0.983 | 1.752 | 0.194 | 1.494 |  |  |  | 6525 | 825 | 0.213 | 7.9091 | -0.071
| 2019-06-17 22:30 | 0 | 0 | 0 | 10.079 | 0.197 | 0.967 | 1.746 | 0.2 | 1.5 |  |  |  | 6540 | 840 | 0.197 | 7.7857 | -0.065
| 2019-06-17 22:45 | 0 | 0 | 0 | 10.115 | 0.21 | 0.98 | 1.751 | 0.195 | 1.495 |  |  |  | 6555 | 855 | 0.21 | 7.6667 | -0.07
| 2019-06-17 23:00 | 0 | 0 | 0 | 10.082 | 0.215 | 0.985 | 1.747 | 0.199 | 1.499 |  |  |  | 6570 | 870 | 0.215 | 7.5517 | -0.066
| 2019-06-17 23:15 | 0 | 0 | 0 | 10.096 | 0.188 | 0.958 | 1.761 | 0.185 | 1.485 |  |  |  | 6585 | 885 | 0.188 | 7.4407 | -0.08
| 2019-06-17 23:30 | 0 | 0 | 0 | 10.101 | 0.205 | 0.975 | 1.763 | 0.183 | 1.483 |  |  |  | 6600 | 900 | 0.205 | 7.3333 | -0.082
| 2019-06-17 23:45 | 0 | 0 | 0 | 10.097 | 0.194 | 0.964 | 1.757 | 0.189 | 1.489 |  |  |  | 6615 | 915 | 0.194 | 7.2295 | -0.076
| 2019-06-18 | 0 | 0 | 0 | 10.111 | 0.187 | 0.957 | 1.749 | 0.197 | 1.497 |  |  |  | 6630 | 930 | 0.187 | 7.129 | -0.068
| 2019-06-18 00:15 | 0 | 0 | 0 | 10.094 | 0.212 | 0.982 | 1.764 | 0.182 | 1.482 |  |  |  | 6645 | 945 | 0.212 | 7.0317 | -0.083
| 2019-06-18 00:30 | 0 | 0 | 0 | 10.091 | 0.19 | 0.96 | 1.754 | 0.192 | 1.492 |  |  |  | 6660 | 960 | 0.19 | 6.9375 | -0.073
| 2019-06-18 00:45 | 0 | 0 | 0 | 10.08 | 0.182 | 0.952 | 1.749 | 0.197 | 1.497 |  |  |  | 6675 | 975 | 0.182 | 6.8462 | -0.068
| 2019-06-18 01:00 | 0 | 0 | 0 | 10.111 | 0.202 | 0.972 | 1.763 | 0.183 | 1.483 |  |  |  | 6690 | 990 | 0.202 | 6.7576 | -0.082
| 2019-06-18 01:15 | 0 | 0 | 0 | 10.088 | 0.173 | 0.943 | 1.762 | 0.184 | 1.484 |  |  |  | 6705 | 1005 | 0.173 | 6.6716 | -0.081
| 2019-06-18 01:30 | 0 | 0 | 0 | 10.089 | 0.179 | 0.949 | 1.765 | 0.181 | 1.481 |  |  |  | 6720 | 1020 | 0.179 | 6.5882 | -0.084
| 2019-06-18 01:45 | 0 | 0 | 0 | 10.081 | 0.171 | 0.941 | 1.756 | 0.19 | 1.49 |  |  |  | 6735 | 1035 | 0.171 | 6.5072 | -0.075
| 2019-06-18 02:00 | 0 | 0 | 0 | 10.096 | 0.182 | 0.952 | 1.767 | 0.179 | 1.479 |  |  |  | 6750 | 1050 | 0.182 | 6.4286 | -0.086
| 2019-06-18 02:15 | 0 | 0 | 0 | 10.089 | 0.165 | 0.935 | 1.765 | 0.181 | 1.481 |  |  |  | 6765 | 1065 | 0.165 | 6.3521 | -0.084
| 2019-06-18 02:30 | 0 | 0 | 0 | 10.105 | 0.163 | 0.933 | 1.763 | 0.183 | 1.483 |  |  |  | 6780 | 1080 | 0.163 | 6.2778 | -0.082
| 2019-06-18 02:45 | 0 | 0 | 0 | 10.111 | 0.184 | 0.954 | 1.758 | 0.188 | 1.488 |  |  |  | 6795 | 1095 | 0.184 | 6.2055 | -0.077
| 2019-06-18 03:00 | 0 | 0 | 0 | 10.087 | 0.185 | 0.955 | 1.754 | 0.192 | 1.492 |  |  |  | 6810 | 1110 | 0.185 | 6.1351 | -0.073
| 2019-06-18 03:15 | 0 | 0 | 0 | 10.114 | 0.169 | 0.939 | 1.756 | 0.19 | 1.49 |  |  |  | 6825 | 1125 | 0.169 | 6.0667 | -0.075
| 2019-06-18 03:30 | 0 | 0 | 0 | 10.097 | 0.182 | 0.952 | 1.763 | 0.183 | 1.483 |  |  |  | 6840 | 1140 | 0.182 | 6 | -0.082
| 2019-06-18 03:45 | 0 | 0 | 0 | 10.082 | 0.17 | 0.94 | 1.759 | 0.187 | 1.487 |  |  |  | 6855 | 1155 | 0.17 | 5.9351 | -0.078
| 2019-06-18 04:00 | 0 | 0 | 0 | 10.097 | 0.161 | 0.931 | 1.771 | 0.175 | 1.475 |  |  |  | 6870 | 1170 | 0.161 | 5.8718 | -0.09
| 2019-06-18 04:15 | 0 | 0 | 0 | 10.091 | 0.183 | 0.953 | 1.768 | 0.178 | 1.478 |  |  |  | 6885 | 1185 | 0.183 | 5.8101 | -0.087
| 2019-06-18 04:30 | 0 | 0 | 0 | 10.084 | 0.154 | 0.924 | 1.756 | 0.19 | 1.49 |  |  |  | 6900 | 1200 | 0.154 | 5.75 | -0.075
| 2019-06-18 04:45 | 0 | 0 | 0 | 10.104 | 0.163 | 0.933 | 1.768 | 0.178 | 1.478 |  |  |  | 6915 | 1215 | 0.163 | 5.6914 | -0.087
| 2019-06-18 05:00 | 0 | 0 | 0 | 10.082 | 0.174 | 0.944 | 1.772 | 0.174 | 1.474 |  |  |  | 6930 | 1230 | 0.174 | 5.6341 | -0.091
| 2019-06-18 05:15 | 0 | 0 | 0 | 10.082 | 0.16 | 0.93 | 1.759 | 0.187 | 1.487 |  |  |  | 6945 | 1245 | 0.16 | 5.5783 | -0.078
| 2019-06-18 05:30 | 0 | 0 | 0 | 10.111 | 0.156 | 0.926 | 1.76 | 0.186 | 1.486 |  |  |  | 6960 | 1260 | 0.156 | 5.5238 | -0.079
| 2019-06-18 05:45 | 0 | 0 | 0 | 10.098 | 0.164 | 0.934 | 1.757 | 0.189 | 1.489 |  |  |  | 6975 | 1275 | 0.164 | 5.4706 | -0.076
| 2019-06-18 06:00 | 0 | 0 | 0 | 10.09 | 0.155 | 0.925 | 1.756 | 0.19 | 1.49 |  |  |  | 6990 | 1290 | 0.155 | 5.4186 | -0.075
| 2019-06-18 06:15 | 0 | 0 | 0 | 10.107 | 0.164 | 0.934 | 1.756 | 0.19 | 1.49 |  |  |  | 7005 | 1305 | 0.164 | 5.3678 | -0.075
| 2019-06-18 06:30 | 0 | 0 | 0 | 10.095 | 0.15 | 0.92 | 1.764 | 0.182 | 1.482 |  |  |  | 7020 | 1320 | 0.15 | 5.3182 | -0.083
| 2019-06-18 06:45 | 0 | 0 | 0 | 10.095 | 0.173 | 0.943 | 1.769 | 0.177 | 1.477 |  |  |  | 7035 | 1335 | 0.173 | 5.2697 | -0.088
| 2019-06-18 07:00 | 0 | 0 | 0 | 10.09 | 0.164 | 0.934 | 1.759 | 0.187 | 1.487 |  |  |  | 7050 | 1350 | 0.164 | 5.2222 | -0.078
| 2019-06-18 07:15 | 0 | 0 | 0 | 10.103 | 0.161 | 0.931 | 1.766 | 0.18 | 1.48 |  |  |  | 7065 | 1365 | 0.161 | 5.1758 | -0.085
| 2019-06-18 07:30 | 0 | 0 | 0 | 10.091 | 0.154 | 0.924 | 1.765 | 0.181 | 1.481 |  |  |  | 7080 | 1380 | 0.154 | 5.1304 | -0.084
| 2019-06-18 07:45 | 0 | 0 | 0 | 10.1 | 0.164 | 0.934 | 1.755 | 0.191 | 1.491 |  |  |  | 7095 | 1395 | 0.164 | 5.086 | -0.074
| 2019-06-18 08:00 | 0 | 0 | 0 | 10.108 | 0.148 | 0.918 | 1.763 | 0.183 | 1.483 |  |  |  | 7110 | 1410 | 0.148 | 5.0426 | -0.082
| 2019-06-18 08:15 | 0 | 0 | 0 | 10.086 | 0.172 | 0.942 | 1.767 | 0.179 | 1.479 |  |  |  | 7125 | 1425 | 0.172 | 5 | -0.086
| 2019-06-18 08:30 | 0 | 0 | 0 | 10.087 | 0.155 | 0.925 | 1.768 | 0.178 | 1.478 |  |  |  | 7140 | 1440 | 0.155 | 4.9583 | -0.087
| 2019-06-18 08:45 | 0 | 0 | 0 | 10.084 | 0.17 | 0.94 | 1.769 | 0.177 | 1.477 |  |  |  | 7155 | 1455 | 0.17 | 4.9175 | -0.088
| 2019-06-18 09:00 | 0 | 0 | 0 | 10.094 | 0.167 | 0.937 | 1.769 | 0.177 | 1.477 | 0.37 | 1.46 | 0.915 | 7170 | 1470 | 0.167 | 4.8776 | -0.088
| 2019-06-18 09:15 | 0 | 0 | 0 | 10.079 | 0.174 | 0.944 | 1.774 | 0.172 | 1.472 |  |  |  | 7185 | 1485 | 0.174 | 4.8384 | -0.093
| 2019-06-18 09:30 | 0 | 0 | 0 | 10.076 | 0.169 | 0.939 | 1.761 | 0.185 | 1.485 |  |  |  | 7200 | 1500 | 0.169 | 4.8 | -0.08
| 2019-06-18 09:45 | 0 | 0 | 0 | 10.086 | 0.18 | 0.95 | 1.762 | 0.184 | 1.484 |  |  |  | 7215 | 1515 | 0.18 | 4.7624 | -0.081
| 2019-06-18 10:00 | 0 | 0 | 0 | 10.09 | 0.172 | 0.942 | 1.78 | 0.166 | 1.466 |  |  |  | 7230 | 1530 | 0.172 | 4.7255 | -0.099
| 2019-06-18 10:15 | 0 | 0 | 0 | 10.068 | 0.179 | 0.949 | 1.765 | 0.181 | 1.481 |  |  |  | 7245 | 1545 | 0.179 | 4.6893 | -0.084
| 2019-06-18 10:30 | 0 | 0 | 0 | 10.091 | 0.174 | 0.944 | 1.78 | 0.166 | 1.466 |  |  |  | 7260 | 1560 | 0.174 | 4.6538 | -0.099
| 2019-06-18 10:45 | 0 | 0 | 0 | 10.108 | 0.184 | 0.954 | 1.764 | 0.182 | 1.482 |  |  |  | 7275 | 1575 | 0.184 | 4.619 | -0.083
| 2019-06-18 11:00 | 0 | 0 | 0 | 10.098 | 0.173 | 0.943 | 1.787 | 0.159 | 1.459 |  |  |  | 7290 | 1590 | 0.173 | 4.5849 | -0.106
| 2019-06-18 11:15 | 0 | 0 | 0 | 10.103 | 0.185 | 0.955 | 1.769 | 0.177 | 1.477 |  |  |  | 7305 | 1605 | 0.185 | 4.5514 | -0.088
| 2019-06-18 11:30 | 0 | 0 | 0 | 10.097 | 0.176 | 0.946 | 1.758 | 0.188 | 1.488 |  |  |  | 7320 | 1620 | 0.176 | 4.5185 | -0.077
| 2019-06-18 11:45 | 0 | 0 | 0 | 10.101 | 0.165 | 0.935 | 1.776 | 0.17 | 1.47 |  |  |  | 7335 | 1635 | 0.165 | 4.4862 | -0.095
| 2019-06-18 12:00 | 0 | 0 | 0 | 10.085 | 0.179 | 0.949 | 1.768 | 0.178 | 1.478 |  |  |  | 7350 | 1650 | 0.179 | 4.4545 | -0.087
| 2019-06-18 12:15 | 0 | 0 | 0 | 10.113 | 0.178 | 0.948 | 1.767 | 0.179 | 1.479 |  |  |  | 7365 | 1665 | 0.178 | 4.4234 | -0.086
| 2019-06-18 12:30 | 0 | 0 | 0 | 10.096 | 0.167 | 0.937 | 1.771 | 0.175 | 1.475 |  |  |  | 7380 | 1680 | 0.167 | 4.3929 | -0.09
| 2019-06-18 12:45 | 0 | 0 | 0 | 10.1 | 0.155 | 0.925 | 1.772 | 0.174 | 1.474 |  |  |  | 7395 | 1695 | 0.155 | 4.3628 | -0.091
| 2019-06-18 13:00 | 0 | 0 | 0 | 10.089 | 0.169 | 0.939 | 1.774 | 0.172 | 1.472 |  |  |  | 7410 | 1710 | 0.169 | 4.3333 | -0.093
| 2019-06-18 13:15 | 0 | 0 | 0 | 10.091 | 0.158 | 0.928 | 1.779 | 0.167 | 1.467 |  |  |  | 7425 | 1725 | 0.158 | 4.3043 | -0.098
| 2019-06-18 13:30 | 0 | 0 | 0 | 10.088 | 0.179 | 0.949 | 1.782 | 0.164 | 1.464 |  |  |  | 7440 | 1740 | 0.179 | 4.2759 | -0.101
| 2019-06-18 13:45 | 0 | 0 | 0 | 10.105 | 0.163 | 0.933 | 1.789 | 0.157 | 1.457 |  |  |  | 7455 | 1755 | 0.163 | 4.2479 | -0.108
| 2019-06-18 14:00 | 0 | 0 | 0 | 10.111 | 0.158 | 0.928 | 1.785 | 0.161 | 1.461 |  |  |  | 7470 | 1770 | 0.158 | 4.2203 | -0.104
| 2019-06-18 14:15 | 0 | 0 | 0 | 10.092 | 0.147 | 0.917 | 1.778 | 0.168 | 1.468 |  |  |  | 7485 | 1785 | 0.147 | 4.1933 | -0.097
| 2019-06-18 14:30 | 0 | 0 | 0 | 10.088 | 0.164 | 0.934 | 1.79 | 0.156 | 1.456 |  |  |  | 7500 | 1800 | 0.164 | 4.1667 | -0.109
| 2019-06-18 14:45 | 0 | 0 | 0 | 10.077 | 0.145 | 0.915 | 1.782 | 0.164 | 1.464 |  |  |  | 7515 | 1815 | 0.145 | 4.1405 | -0.101
| 2019-06-18 15:00 | 0 | 0 | 0 | 10.094 | 0.146 | 0.916 | 1.787 | 0.159 | 1.459 |  |  |  | 7530 | 1830 | 0.146 | 4.1148 | -0.106
| 2019-06-18 15:15 | 0 | 0 | 0 | 10.1 | 0.155 | 0.925 | 1.772 | 0.174 | 1.474 |  |  |  | 7545 | 1845 | 0.155 | 4.0894 | -0.091
| 2019-06-18 15:30 | 0 | 0 | 0 | 10.103 | 0.147 | 0.917 | 1.786 | 0.16 | 1.46 |  |  |  | 7560 | 1860 | 0.147 | 4.0645 | -0.105
| 2019-06-18 15:45 | 0 | 0 | 0 | 10.094 | 0.156 | 0.926 | 1.772 | 0.174 | 1.474 |  |  |  | 7575 | 1875 | 0.156 | 4.04 | -0.091
| 2019-06-18 16:00 | 0 | 0 | 0 | 10.105 | 0.124 | 0.894 | 1.771 | 0.175 | 1.475 |  |  |  | 7590 | 1890 | 0.124 | 4.0159 | -0.09
| 2019-06-18 16:15 | 0 | 0 | 0 | 10.091 | 0.138 | 0.908 | 1.772 | 0.174 | 1.474 |  |  |  | 7605 | 1905 | 0.138 | 3.9921 | -0.091
| 2019-06-18 16:30 | 0 | 0 | 0 | 10.081 | 0.151 | 0.921 | 1.776 | 0.17 | 1.47 |  |  |  | 7620 | 1920 | 0.151 | 3.9688 | -0.095
| 2019-06-18 16:45 | 0 | 0 | 0 | 10.088 | 0.142 | 0.912 | 1.776 | 0.17 | 1.47 |  |  |  | 7635 | 1935 | 0.142 | 3.9457 | -0.095
| 2019-06-18 17:00 | 0 | 0 | 0 | 10.101 | 0.137 | 0.907 | 1.778 | 0.168 | 1.468 |  |  |  | 7650 | 1950 | 0.137 | 3.9231 | -0.097
| 2019-06-18 17:15 | 0 | 0 | 0 | 10.12 | 0.136 | 0.906 | 1.785 | 0.161 | 1.461 |  |  |  | 7665 | 1965 | 0.136 | 3.9008 | -0.104
| 2019-06-18 17:30 | 0 | 0 | 0 | 10.088 | 0.137 | 0.907 | 1.793 | 0.153 | 1.453 |  |  |  | 7680 | 1980 | 0.137 | 3.8788 | -0.112
| 2019-06-18 17:45 | 0 | 0 | 0 | 10.1 | 0.123 | 0.893 | 1.785 | 0.161 | 1.461 |  |  |  | 7695 | 1995 | 0.123 | 3.8571 | -0.104
| 2019-06-18 18:00 | 0 | 0 | 0 | 10.105 | 0.138 | 0.908 | 1.779 | 0.167 | 1.467 |  |  |  | 7710 | 2010 | 0.138 | 3.8358 | -0.098
| 2019-06-18 18:15 | 0 | 0 | 0 | 10.081 | 0.141 | 0.911 | 1.78 | 0.166 | 1.466 |  |  |  | 7725 | 2025 | 0.141 | 3.8148 | -0.099
| 2019-06-18 18:30 | 0 | 0 | 0 | 10.105 | 0.126 | 0.896 | 1.777 | 0.169 | 1.469 |  |  |  | 7740 | 2040 | 0.126 | 3.7941 | -0.096
| 2019-06-18 18:45 | 0 | 0 | 0 | 10.08 | 0.141 | 0.911 | 1.789 | 0.157 | 1.457 |  |  |  | 7755 | 2055 | 0.141 | 3.7737 | -0.108
| 2019-06-18 19:00 | 0 | 0 | 0 | 10.094 | 0.143 | 0.913 | 1.785 | 0.161 | 1.461 |  |  |  | 7770 | 2070 | 0.143 | 3.7536 | -0.104
| 2019-06-18 19:15 | 0 | 0 | 0 | 10.085 | 0.151 | 0.921 | 1.795 | 0.151 | 1.451 |  |  |  | 7785 | 2085 | 0.151 | 3.7338 | -0.114
| 2019-06-18 19:30 | 0 | 0 | 0 | 10.077 | 0.133 | 0.903 | 1.781 | 0.165 | 1.465 |  |  |  | 7800 | 2100 | 0.133 | 3.7143 | -0.1
| 2019-06-18 19:45 | 0 | 0 | 0 | 10.111 | 0.137 | 0.907 | 1.781 | 0.165 | 1.465 |  |  |  | 7815 | 2115 | 0.137 | 3.695 | -0.1
| 2019-06-18 20:00 | 0 | 0 | 0 | 10.089 | 0.143 | 0.913 | 1.793 | 0.153 | 1.453 |  |  |  | 7830 | 2130 | 0.143 | 3.6761 | -0.112
| 2019-06-18 20:15 | 0 | 0 | 0 | 10.091 | 0.153 | 0.923 | 1.772 | 0.174 | 1.474 |  |  |  | 7845 | 2145 | 0.153 | 3.6573 | -0.091
| 2019-06-18 20:30 | 0 | 0 | 0 | 10.107 | 0.142 | 0.912 | 1.785 | 0.161 | 1.461 |  |  |  | 7860 | 2160 | 0.142 | 3.6389 | -0.104
| 2019-06-18 20:45 | 0 | 0 | 0 | 10.097 | 0.132 | 0.902 | 1.785 | 0.161 | 1.461 |  |  |  | 7875 | 2175 | 0.132 | 3.6207 | -0.104
| 2019-06-18 21:00 | 0 | 0 | 0 | 10.094 | 0.143 | 0.913 | 1.802 | 0.144 | 1.444 |  |  |  | 7890 | 2190 | 0.143 | 3.6027 | -0.121
| 2019-06-18 21:15 | 0 | 0 | 0 | 10.091 | 0.129 | 0.899 | 1.78 | 0.166 | 1.466 |  |  |  | 7905 | 2205 | 0.129 | 3.585 | -0.099
| 2019-06-18 21:30 | 0 | 0 | 0 | 10.105 | 0.139 | 0.909 | 1.786 | 0.16 | 1.46 |  |  |  | 7920 | 2220 | 0.139 | 3.5676 | -0.105
| 2019-06-18 21:45 | 0 | 0 | 0 | 10.089 | 0.141 | 0.911 | 1.787 | 0.159 | 1.459 |  |  |  | 7935 | 2235 | 0.141 | 3.5503 | -0.106
| 2019-06-18 22:00 | 0 | 0 | 0 | 10.083 | 0.142 | 0.912 | 1.795 | 0.151 | 1.451 |  |  |  | 7950 | 2250 | 0.142 | 3.5333 | -0.114
| 2019-06-18 22:15 | 0 | 0 | 0 | 10.086 | 0.138 | 0.908 | 1.791 | 0.155 | 1.455 |  |  |  | 7965 | 2265 | 0.138 | 3.5166 | -0.11
| 2019-06-18 22:30 | 0 | 0 | 0 | 10.084 | 0.144 | 0.914 | 1.779 | 0.167 | 1.467 |  |  |  | 7980 | 2280 | 0.144 | 3.5 | -0.098
| 2019-06-18 22:45 | 0 | 0 | 0 | 10.093 | 0.153 | 0.923 | 1.784 | 0.162 | 1.462 |  |  |  | 7995 | 2295 | 0.153 | 3.4837 | -0.103
| 2019-06-18 23:00 | 0 | 0 | 0 | 10.088 | 0.15 | 0.92 | 1.772 | 0.174 | 1.474 |  |  |  | 8010 | 2310 | 0.15 | 3.4675 | -0.091
| 2019-06-18 23:15 | 0 | 0 | 0 | 10.093 | 0.156 | 0.926 | 1.778 | 0.168 | 1.468 |  |  |  | 8025 | 2325 | 0.156 | 3.4516 | -0.097
| 2019-06-18 23:30 | 0 | 0 | 0 | 10.083 | 0.155 | 0.925 | 1.79 | 0.156 | 1.456 |  |  |  | 8040 | 2340 | 0.155 | 3.4359 | -0.109
| 2019-06-18 23:45 | 0 | 0 | 0 | 10.088 | 0.15 | 0.92 | 1.797 | 0.149 | 1.449 |  |  |  | 8055 | 2355 | 0.15 | 3.4204 | -0.116
| 2019-06-19 | 0 | 0 | 0 | 10.091 | 0.163 | 0.933 | 1.792 | 0.154 | 1.454 |  |  |  | 8070 | 2370 | 0.163 | 3.4051 | -0.111
| 2019-06-19 00:15 | 0 | 0 | 0 | 10.105 | 0.151 | 0.921 | 1.785 | 0.161 | 1.461 |  |  |  | 8085 | 2385 | 0.151 | 3.3899 | -0.104
| 2019-06-19 00:30 | 0 | 0 | 0 | 10.103 | 0.156 | 0.926 | 1.794 | 0.152 | 1.452 |  |  |  | 8100 | 2400 | 0.156 | 3.375 | -0.113
| 2019-06-19 00:45 | 0 | 0 | 0 | 10.098 | 0.163 | 0.933 | 1.789 | 0.157 | 1.457 |  |  |  | 8115 | 2415 | 0.163 | 3.3602 | -0.108
| 2019-06-19 01:00 | 0 | 0 | 0 | 10.094 | 0.144 | 0.914 | 1.791 | 0.155 | 1.455 |  |  |  | 8130 | 2430 | 0.144 | 3.3457 | -0.11
| 2019-06-19 01:15 | 0 | 0 | 0 | 10.083 | 0.147 | 0.917 | 1.783 | 0.163 | 1.463 |  |  |  | 8145 | 2445 | 0.147 | 3.3313 | -0.102
| 2019-06-19 01:30 | 0 | 0 | 0 | 10.1 | 0.162 | 0.932 | 1.792 | 0.154 | 1.454 |  |  |  | 8160 | 2460 | 0.162 | 3.3171 | -0.111
| 2019-06-19 01:45 | 0 | 0 | 0 | 10.109 | 0.162 | 0.932 | 1.81 | 0.136 | 1.436 |  |  |  | 8175 | 2475 | 0.162 | 3.303 | -0.129
| 2019-06-19 02:00 | 0 | 0 | 0 | 10.091 | 0.158 | 0.928 | 1.8 | 0.146 | 1.446 |  |  |  | 8190 | 2490 | 0.158 | 3.2892 | -0.119
| 2019-06-19 02:15 | 0 | 0 | 0 | 10.103 | 0.153 | 0.923 | 1.789 | 0.157 | 1.457 |  |  |  | 8205 | 2505 | 0.153 | 3.2754 | -0.108
| 2019-06-19 02:30 | 0 | 0 | 0 | 10.091 | 0.164 | 0.934 | 1.801 | 0.145 | 1.445 |  |  |  | 8220 | 2520 | 0.164 | 3.2619 | -0.12
| 2019-06-19 02:45 | 0 | 0 | 0 | 10.078 | 0.154 | 0.924 | 1.8 | 0.146 | 1.446 |  |  |  | 8235 | 2535 | 0.154 | 3.2485 | -0.119
| 2019-06-19 03:00 | 0 | 0 | 0 | 10.101 | 0.151 | 0.921 | 1.802 | 0.144 | 1.444 |  |  |  | 8250 | 2550 | 0.151 | 3.2353 | -0.121
| 2019-06-19 03:15 | 0 | 0 | 0 | 10.106 | 0.147 | 0.917 | 1.794 | 0.152 | 1.452 |  |  |  | 8265 | 2565 | 0.147 | 3.2222 | -0.113
| 2019-06-19 03:30 | 0 | 0 | 0 | 10.101 | 0.148 | 0.918 | 1.799 | 0.147 | 1.447 |  |  |  | 8280 | 2580 | 0.148 | 3.2093 | -0.118
| 2019-06-19 03:45 | 0 | 0 | 0 | 10.099 | 0.145 | 0.915 | 1.809 | 0.137 | 1.437 |  |  |  | 8295 | 2595 | 0.145 | 3.1965 | -0.128
| 2019-06-19 04:00 | 0 | 0 | 0 | 10.12 | 0.152 | 0.922 | 1.793 | 0.153 | 1.453 |  |  |  | 8310 | 2610 | 0.152 | 3.1839 | -0.112
| 2019-06-19 04:15 | 0 | 0 | 0 | 10.111 | 0.168 | 0.938 | 1.804 | 0.142 | 1.442 |  |  |  | 8325 | 2625 | 0.168 | 3.1714 | -0.123
| 2019-06-19 04:30 | 0 | 0 | 0 | 10.096 | 0.155 | 0.925 | 1.8 | 0.146 | 1.446 |  |  |  | 8340 | 2640 | 0.155 | 3.1591 | -0.119
| 2019-06-19 04:45 | 0 | 0 | 0 | 10.094 | 0.147 | 0.917 | 1.796 | 0.15 | 1.45 |  |  |  | 8355 | 2655 | 0.147 | 3.1469 | -0.115
| 2019-06-19 05:00 | 0 | 0 | 0 | 10.094 | 0.144 | 0.914 | 1.786 | 0.16 | 1.46 |  |  |  | 8370 | 2670 | 0.144 | 3.1348 | -0.105
| 2019-06-19 05:15 | 0 | 0 | 0 | 10.095 | 0.146 | 0.916 | 1.799 | 0.147 | 1.447 |  |  |  | 8385 | 2685 | 0.146 | 3.1229 | -0.118
| 2019-06-19 05:30 | 0 | 0 | 0 | 10.097 | 0.16 | 0.93 | 1.798 | 0.148 | 1.448 |  |  |  | 8400 | 2700 | 0.16 | 3.1111 | -0.117
| 2019-06-19 05:45 | 0 | 0 | 0 | 10.109 | 0.154 | 0.924 | 1.812 | 0.134 | 1.434 |  |  |  | 8415 | 2715 | 0.154 | 3.0994 | -0.131
| 2019-06-19 06:00 | 0 | 0 | 0 | 10.079 | 0.153 | 0.923 | 1.797 | 0.149 | 1.449 |  |  |  | 8430 | 2730 | 0.153 | 3.0879 | -0.116
| 2019-06-19 06:15 | 0 | 0 | 0 | 10.093 | 0.153 | 0.923 | 1.808 | 0.138 | 1.438 |  |  |  | 8445 | 2745 | 0.153 | 3.0765 | -0.127
| 2019-06-19 06:30 | 0 | 0 | 0 | 10.104 | 0.152 | 0.922 | 1.805 | 0.141 | 1.441 |  |  |  | 8460 | 2760 | 0.152 | 3.0652 | -0.124
| 2019-06-19 06:45 | 0 | 0 | 0 | 10.085 | 0.156 | 0.926 | 1.798 | 0.148 | 1.448 |  |  |  | 8475 | 2775 | 0.156 | 3.0541 | -0.117
| 2019-06-19 07:00 | 0 | 0 | 0 | 10.104 | 0.167 | 0.937 | 1.794 | 0.152 | 1.452 |  |  |  | 8490 | 2790 | 0.167 | 3.043 | -0.113
| 2019-06-19 07:15 | 0 | 0 | 0 | 10.089 | 0.163 | 0.933 | 1.806 | 0.14 | 1.44 |  |  |  | 8505 | 2805 | 0.163 | 3.0321 | -0.125
| 2019-06-19 07:30 | 0 | 0 | 0 | 10.097 | 0.167 | 0.937 | 1.799 | 0.147 | 1.447 |  |  |  | 8520 | 2820 | 0.167 | 3.0213 | -0.118
| 2019-06-19 07:45 | 0 | 0 | 0 | 10.094 | 0.159 | 0.929 | 1.809 | 0.137 | 1.437 |  |  |  | 8535 | 2835 | 0.159 | 3.0106 | -0.128
| 2019-06-19 08:00 | 0 | 0 | 0 | 10.098 | 0.155 | 0.925 | 1.803 | 0.143 | 1.443 |  |  |  | 8550 | 2850 | 0.155 | 3 | -0.122
End of recovery test | 2019-06-19 08:15 | 0 | 0 | 0 | 10.085 | 0.183 | 0.953 | 1.812 | 0.134 | 1.434 |  |  |  | 8565 | 2865 | 0.183 | 2.9895 | -0.131
Note on H1: Eileen Vilasenor: Data corrected to account for 0.77 mbwt datum reference.
Note on K1: Eileen Vilasenor: Data corrected - raw data was flipped across the horizontal axis. Then 1.5m was added to match the manual data.
Note on N437: Eileen Vilasenor: Corrected to account for 0.77 mbwt

## Calculations
Used for BH4 Hydrograph
CRT Start | 2019-06-15 10:00 | 0 | Flow rate BH5 (CRT period) | Average flow rate (m3/hr) | Transmissivity (m2/hr) | 3.2538
| 2019-06-15 10:00 | 3 | 1.668 | 1.5928 | Average abstraction Q (m3/hr) | 1.6
CRT End | 2019-06-17 08:30 | 0 | 1.656 |  | delta s (m) | 0.09
| 2019-06-17 08:30 | 3 | 1.644 |  | Transmissivity (m2/d) | 78.092
1.644
|  |  | 1.644 |  | Storage (dimensionless) | 0.069265
|  |  | 1.644 |  | Transmissivity T (m2/day) | 78.092
|  |  | 1.62 |  | t0 (time intercept) | 1.64
|  |  | 1.632 |  | r (distance to PBH) | 64.5
1.632
|  |  | 1.62 |  | 0.5625
1.632
1.62
1.62
1.62
1.62
1.608
1.62
1.608
1.608
1.608
1.608
1.608
1.608
1.608
1.596
1.596
1.596
1.608
1.608
1.608
1.596
1.596
1.608
1.596
1.608
1.608
1.596
1.596
1.596
1.596
1.596
1.596
1.596
1.596
1.608
1.572
1.584
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.596
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.596
1.584
1.584
1.584
1.596
1.584
1.584
1.584
1.596
1.584
1.584
1.584
1.596
1.596
1.584
1.596
1.596
1.596
1.584
1.596
1.584
1.596
1.584
1.584
1.596
1.584
1.584
1.584
1.596
1.596
1.584
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.596
1.584
1.584
1.596
1.596
1.584
1.584
1.596
1.596
1.584
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.572
1.584
1.584
1.584
1.584
1.596
1.596
1.596
1.596
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.596
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.572
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.584
1.572
1.584
1.584
1.572
1.596
1.584
1.584
1.584
1.584
1.584
1.572
1.584
1.584
1.572
1.584
1.584
1.56

## Rainfall data
Date | Daily Rainfall (mm) | Source: | Met Office | https://www.metoffice.gov.uk/hadobs/hadukp/data/download.html
2019-06-01 | 1.68
2019-06-02 | 0.88
2019-06-03 | 1.1
2019-06-04 | 13.01
2019-06-05 | 0.94
2019-06-06 | 1.33
2019-06-07 | 24.63
2019-06-08 | 3.99
2019-06-09 | 0.61
2019-06-10 | 4.13
2019-06-11 | 20.41
2019-06-12 | 10.55
2019-06-13 | 5.09
2019-06-14 | 1.23
2019-06-15 | 2.4
2019-06-16 | 7.15
2019-06-17 | 0.29
2019-06-18 | 3.03
2019-06-19 | 0.7
2019-06-20 | 0.57
2019-06-21 | 0
2019-06-22 | 0
2019-06-23 | 8.42
2019-06-24 | 1.02
2019-06-25 | 2.16
2019-06-26 | 0
2019-06-27 | 0
2019-06-28 | 0
2019-06-29 | 0.25
2019-06-30 | 0.28

## Raw Data
Raw data | BH5 | 24.06.2019 | -11858
Date and Time | Count | ltr/hr | M3/hr | Temperature (C) | Level Depth To Water (m) BH5 | Level Depth To Water (m) BH4 | BH1 Manual read | BH 4 Manual Read | BH 5 Manual Read
2019-06-12 09:00 | 144 | 1728 | 1.728 | 10.098 | 29.764 | 1.946
2019-06-12 09:15 | 144 | 1728 | 1.728 | 10.083 | 29.752 | 1.948
2019-06-12 09:30 | 144 | 1728 | 1.728 | 10.089 | 29.964 | 1.945
2019-06-12 09:45 | 145 | 1740 | 1.74 | 10.085 | 29.867 | 1.936
2019-06-12 10:00 | 144 | 1728 | 1.728 | 10.103 | 29.852 | 1.947
2019-06-12 10:15 | 144 | 1728 | 1.728 | 10.096 | 29.826 | 1.941
2019-06-12 10:30 | 144 | 1728 | 1.728 | 10.097 | 29.771 | 1.931
2019-06-12 10:45 | 144 | 1728 | 1.728 | 10.097 | 29.736 | 1.925
2019-06-12 11:00 | 143 | 1716 | 1.716 | 10.097 | 29.704 | 1.94
2019-06-12 11:15 | 145 | 1740 | 1.74 | 10.093 | 29.71 | 1.93
2019-06-12 11:30 | 144 | 1728 | 1.728 | 10.101 | 29.696 | 1.932
2019-06-12 11:45 | 144 | 1728 | 1.728 | 10.094 | 29.698 | 1.928
2019-06-12 12:00 | 145 | 1740 | 1.74 | 10.083 | 29.691 | 1.925
2019-06-12 12:15 | 143 | 1716 | 1.716 | 10.081 | 29.634 | 1.92
2019-06-12 12:30 | 144 | 1728 | 1.728 | 10.078 | 29.67 | 1.926
2019-06-12 12:45 | 144 | 1728 | 1.728 | 10.104 | 29.676 | 1.928
2019-06-12 13:00 | 145 | 1740 | 1.74 | 10.091 | 29.689 | 1.913
2019-06-12 13:15 | 145 | 1740 | 1.74 | 10.096 | 29.693 | 1.918
2019-06-12 13:30 | 145 | 1740 | 1.74 | 10.083 | 29.7 | 1.906
2019-06-12 13:45 | 144 | 1728 | 1.728 | 10.097 | 29.649 | 1.906
2019-06-12 14:00 | 145 | 1740 | 1.74 | 10.1 | 29.652 | 1.902
2019-06-12 14:15 | 145 | 1740 | 1.74 | 10.101 | 29.617 | 1.904
2019-06-12 14:30 | 144 | 1728 | 1.728 | 10.088 | 29.583 | 1.913
2019-06-12 14:45 | 145 | 1740 | 1.74 | 10.086 | 29.621 | 1.894
2019-06-12 15:00 | 144 | 1728 | 1.728 | 10.08 | 29.602 | 1.917
2019-06-12 15:15 | 145 | 1740 | 1.74 | 10.088 | 29.611 | 1.906
2019-06-12 15:30 | 144 | 1728 | 1.728 | 10.093 | 29.565 | 1.913
2019-06-12 15:45 | 145 | 1740 | 1.74 | 10.098 | 29.565 | 1.909
2019-06-12 16:00 | 145 | 1740 | 1.74 | 10.091 | 29.594 | 1.917
2019-06-12 16:15 | 145 | 1740 | 1.74 | 10.099 | 29.605 | 1.909
2019-06-12 16:30 | 145 | 1740 | 1.74 | 10.116 | 29.613 | 1.917
2019-06-12 16:45 | 145 | 1740 | 1.74 | 10.101 | 29.57 | 1.91
2019-06-12 17:00 | 144 | 1728 | 1.728 | 10.112 | 29.565 | 1.899
2019-06-12 17:15 | 144 | 1728 | 1.728 | 10.094 | 29.554 | 1.899
2019-06-12 17:30 | 145 | 1740 | 1.74 | 10.092 | 29.538 | 1.898
2019-06-12 17:45 | 145 | 1740 | 1.74 | 10.085 | 29.567 | 1.918
2019-06-12 18:00 | 145 | 1740 | 1.74 | 10.097 | 29.57 | 1.901
2019-06-12 18:15 | 145 | 1740 | 1.74 | 10.071 | 29.57 | 1.904
2019-06-12 18:30 | 145 | 1740 | 1.74 | 10.081 | 29.57 | 1.902
2019-06-12 18:45 | 144 | 1728 | 1.728 | 10.09 | 29.554 | 1.892
2019-06-12 19:00 | 146 | 1752 | 1.752 | 10.081 | 29.607 | 1.904
2019-06-12 19:15 | 146 | 1752 | 1.752 | 10.093 | 29.595 | 1.904
2019-06-12 19:30 | 145 | 1740 | 1.74 | 10.085 | 29.561 | 1.895
2019-06-12 19:45 | 145 | 1740 | 1.74 | 10.079 | 29.565 | 1.904
2019-06-12 20:00 | 145 | 1740 | 1.74 | 10.083 | 29.552 | 1.908
2019-06-12 20:15 | 145 | 1740 | 1.74 | 10.105 | 29.554 | 1.895
2019-06-12 20:30 | 145 | 1740 | 1.74 | 10.091 | 29.554 | 1.898
2019-06-12 20:45 | 145 | 1740 | 1.74 | 10.105 | 29.547 | 1.9
2019-06-12 21:00 | 145 | 1740 | 1.74 | 10.103 | 29.561 | 1.889
2019-06-12 21:15 | 145 | 1740 | 1.74 | 10.083 | 29.538 | 1.887
2019-06-12 21:30 | 145 | 1740 | 1.74 | 10.083 | 29.539 | 1.873
2019-06-12 21:45 | 145 | 1740 | 1.74 | 10.096 | 29.547 | 1.867
2019-06-12 22:00 | 146 | 1752 | 1.752 | 10.113 | 29.533 | 1.866
2019-06-12 22:15 | 144 | 1728 | 1.728 | 10.097 | 29.521 | 1.864
2019-06-12 22:30 | 146 | 1752 | 1.752 | 10.085 | 29.523 | 1.858
2019-06-12 22:45 | 145 | 1740 | 1.74 | 10.092 | 29.528 | 1.85
2019-06-12 23:00 | 145 | 1740 | 1.74 | 10.084 | 29.516 | 1.862
2019-06-12 23:15 | 145 | 1740 | 1.74 | 10.081 | 29.511 | 1.85
2019-06-12 23:30 | 145 | 1740 | 1.74 | 10.094 | 29.519 | 1.857
2019-06-12 23:45 | 144 | 1728 | 1.728 | 10.074 | 29.506 | 1.866
2019-06-13 | 145 | 1740 | 1.74 | 10.08 | 29.499 | 1.862
2019-06-13 00:15 | 145 | 1740 | 1.74 | 10.083 | 29.494 | 1.867
2019-06-13 00:30 | 145 | 1740 | 1.74 | 10.107 | 29.501 | 1.843
2019-06-13 00:45 | 145 | 1740 | 1.74 | 10.094 | 29.499 | 1.849
2019-06-13 01:00 | 145 | 1740 | 1.74 | 10.093 | 29.492 | 1.854
2019-06-13 01:15 | 145 | 1740 | 1.74 | 10.085 | 29.501 | 1.827
2019-06-13 01:30 | 145 | 1740 | 1.74 | 10.094 | 29.49 | 1.843
2019-06-13 01:45 | 145 | 1740 | 1.74 | 10.098 | 29.49 | 1.856
2019-06-13 02:00 | 146 | 1752 | 1.752 | 10.097 | 29.494 | 1.859
2019-06-13 02:15 | 145 | 1740 | 1.74 | 10.077 | 29.49 | 1.844
2019-06-13 02:30 | 145 | 1740 | 1.74 | 10.095 | 29.489 | 1.827
2019-06-13 02:45 | 144 | 1728 | 1.728 | 10.087 | 29.477 | 1.829
2019-06-13 03:00 | 145 | 1740 | 1.74 | 10.083 | 29.482 | 1.838
2019-06-13 03:15 | 145 | 1740 | 1.74 | 10.088 | 29.483 | 1.802
2019-06-13 03:30 | 145 | 1740 | 1.74 | 10.09 | 29.458 | 1.792
2019-06-13 03:45 | 146 | 1752 | 1.752 | 10.094 | 29.449 | 1.797
2019-06-13 04:00 | 145 | 1740 | 1.74 | 10.093 | 29.452 | 1.792
2019-06-13 04:15 | 145 | 1740 | 1.74 | 10.098 | 29.445 | 1.764
2019-06-13 04:30 | 145 | 1740 | 1.74 | 10.084 | 29.449 | 1.781
2019-06-13 04:45 | 145 | 1740 | 1.74 | 10.071 | 29.442 | 1.767
2019-06-13 05:00 | 146 | 1752 | 1.752 | 10.083 | 29.433 | 1.751
2019-06-13 05:15 | 144 | 1728 | 1.728 | 10.085 | 29.412 | 1.75
2019-06-13 05:30 | 146 | 1752 | 1.752 | 10.097 | 29.422 | 1.739
2019-06-13 05:45 | 145 | 1740 | 1.74 | 10.116 | 29.399 | 1.738
2019-06-13 06:00 | 145 | 1740 | 1.74 | 10.082 | 29.397 | 1.747
2019-06-13 06:15 | 145 | 1740 | 1.74 | 10.093 | 29.389 | 1.734
2019-06-13 06:30 | 145 | 1740 | 1.74 | 10.1 | 29.353 | 1.715
2019-06-13 06:45 | 144 | 1728 | 1.728 | 10.103 | 29.333 | 1.71
2019-06-13 07:00 | 144 | 1728 | 1.728 | 10.103 | 29.319 | 1.696
2019-06-13 07:15 | 145 | 1740 | 1.74 | 10.092 | 29.31 | 1.699
2019-06-13 07:30 | 145 | 1740 | 1.74 | 10.095 | 29.333 | 1.686
2019-06-13 07:45 | 145 | 1740 | 1.74 | 10.097 | 29.28 | 1.684
2019-06-13 08:00 | 144 | 1728 | 1.728 | 10.087 | 29.285 | 1.676
2019-06-13 08:15 | 145 | 1740 | 1.74 | 10.085 | 29.29 | 1.686
2019-06-13 08:30 | 145 | 1740 | 1.74 | 10.1 | 29.316 | 1.704
2019-06-13 08:45 | 145 | 1740 | 1.74 | 10.08 | 29.478 | 1.71
2019-06-13 09:00 | 144 | 1728 | 1.728 | 10.083 | 25.017 | 1.708 | 0.56 | 1.66 | 29.6
2019-06-13 09:15 | 0 | 0 | 0 | 10.087 | 20.577 | 1.704
2019-06-13 09:30 | 0 | 0 | 0 | 10.092 | 17.542 | 1.694
2019-06-13 09:45 | 0 | 0 | 0 | 10.104 | 14.239 | 1.686
2019-06-13 10:00 | 0 | 0 | 0 | 10.114 | 11.254 | 1.667
2019-06-13 10:15 | 0 | 0 | 0 | 10.094 | 8.974 | 1.66
2019-06-13 10:30 | 0 | 0 | 0 | 10.079 | 7.06 | 1.658
2019-06-13 10:45 | 0 | 0 | 0 | 10.091 | 5.336 | 1.656
2019-06-13 11:00 | 0 | 0 | 0 | 10.074 | 4.127 | 1.639
2019-06-13 11:15 | 0 | 0 | 0 | 10.088 | 3.29 | 1.64
2019-06-13 11:30 | 0 | 0 | 0 | 10.092 | 2.643 | 1.628
2019-06-13 11:45 | 0 | 0 | 0 | 10.108 | 2.146 | 1.623
2019-06-13 12:00 | 0 | 0 | 0 | 10.092 | 1.849 | 1.623
2019-06-13 12:15 | 0 | 0 | 0 | 10.094 | 1.652 | 1.608
2019-06-13 12:30 | 0 | 0 | 0 | 10.089 | 1.44 | 1.606
2019-06-13 12:45 | 0 | 0 | 0 | 10.111 | 1.269 | 1.597
2019-06-13 13:00 | 0 | 0 | 0 | 10.091 | 1.136 | 1.602
2019-06-13 13:15 | 0 | 0 | 0 | 10.097 | 0.984 | 1.608
2019-06-13 13:30 | 0 | 0 | 0 | 10.106 | 0.848 | 1.591
2019-06-13 13:45 | 0 | 0 | 0 | 10.094 | 0.774 | 1.588
2019-06-13 14:00 | 0 | 0 | 0 | 10.105 | 0.679 | 1.582
2019-06-13 14:15 | 0 | 0 | 0 | 10.088 | 0.595 | 1.584
2019-06-13 14:30 | 0 | 0 | 0 | 10.083 | 0.539 | 1.578
2019-06-13 14:45 | 0 | 0 | 0 | 10.094 | 0.494 | 1.575
2019-06-13 15:00 | 0 | 0 | 0 | 10.08 | 0.424 | 1.568
2019-06-13 15:15 | 0 | 0 | 0 | 10.103 | 0.389 | 1.573
2019-06-13 15:30 | 0 | 0 | 0 | 10.102 | 0.352 | 1.566
2019-06-13 15:45 | 0 | 0 | 0 | 10.094 | 0.312 | 1.565
2019-06-13 16:00 | 0 | 0 | 0 | 10.104 | 0.288 | 1.565
2019-06-13 16:15 | 0 | 0 | 0 | 10.084 | 0.249 | 1.559
2019-06-13 16:30 | 0 | 0 | 0 | 10.1 | 0.213 | 1.561
2019-06-13 16:45 | 0 | 0 | 0 | 10.094 | 0.182 | 1.558
2019-06-13 17:00 | 0 | 0 | 0 | 10.104 | 0.145 | 1.551
2019-06-13 17:15 | 0 | 0 | 0 | 10.068 | 0.136 | 1.552
2019-06-13 17:30 | 0 | 0 | 0 | 10.085 | 0.109 | 1.55
2019-06-13 17:45 | 0 | 0 | 0 | 10.097 | 0.097 | 1.548
2019-06-13 18:00 | 0 | 0 | 0 | 10.085 | 0.07 | 1.545
2019-06-13 18:15 | 0 | 0 | 0 | 10.098 | 0.059 | 1.551
2019-06-13 18:30 | 0 | 0 | 0 | 10.099 | 0.058 | 1.536
2019-06-13 18:45 | 0 | 0 | 0 | 10.095 | 0.07 | 1.556
2019-06-13 19:00 | 0 | 0 | 0 | 10.103 | 0.05 | 1.542
2019-06-13 19:15 | 0 | 0 | 0 | 10.12 | 0.069 | 1.549
2019-06-13 19:30 | 0 | 0 | 0 | 10.106 | 0.064 | 1.546
2019-06-13 19:45 | 0 | 0 | 0 | 10.103 | 0.058 | 1.538
2019-06-13 20:00 | 0 | 0 | 0 | 10.11 | 0 | 1.55
2019-06-13 20:15 | 0 | 0 | 0 | 10.09 | 0 | 1.539
2019-06-13 20:30 | 0 | 0 | 0 | 10.089 | 0 | 1.552
2019-06-13 20:45 | 0 | 0 | 0 | 10.084 | 0 | 1.538
2019-06-13 21:00 | 0 | 0 | 0 | 10.094 | 0 | 1.538
2019-06-13 21:15 | 0 | 0 | 0 | 10.115 | 0 | 1.536
2019-06-13 21:30 | 0 | 0 | 0 | 10.103 | 0 | 1.532
2019-06-13 21:45 | 0 | 0 | 0 | 10.089 | 0 | 1.534
2019-06-13 22:00 | 0 | 0 | 0 | 10.096 | 0 | 1.537
2019-06-13 22:15 | 0 | 0 | 0 | 10.1 | 0 | 1.539
2019-06-13 22:30 | 0 | 0 | 0 | 10.104 | 0 | 1.535
2019-06-13 22:45 | 0 | 0 | 0 | 10.094 | 0 | 1.522
2019-06-13 23:00 | 0 | 0 | 0 | 10.086 | 0 | 1.537
2019-06-13 23:15 | 0 | 0 | 0 | 10.089 | 0 | 1.527
2019-06-13 23:30 | 0 | 0 | 0 | 10.099 | 0 | 1.532
2019-06-13 23:45 | 0 | 0 | 0 | 10.098 | 0 | 1.535
2019-06-14 | 0 | 0 | 0 | 10.1 | 0 | 1.529
2019-06-14 00:15 | 0 | 0 | 0 | 10.096 | 0 | 1.525
2019-06-14 00:30 | 0 | 0 | 0 | 10.094 | 0 | 1.531
2019-06-14 00:45 | 0 | 0 | 0 | 10.091 | 0 | 1.536
2019-06-14 01:00 | 0 | 0 | 0 | 10.088 | 0 | 1.533
2019-06-14 01:15 | 0 | 0 | 0 | 10.081 | 0 | 1.533
2019-06-14 01:30 | 0 | 0 | 0 | 10.097 | 0 | 1.537
2019-06-14 01:45 | 0 | 0 | 0 | 10.099 | 0 | 1.511
2019-06-14 02:00 | 0 | 0 | 0 | 10.086 | 0 | 1.532
2019-06-14 02:15 | 0 | 0 | 0 | 10.074 | 0 | 1.519
2019-06-14 02:30 | 0 | 0 | 0 | 10.094 | 0 | 1.536
2019-06-14 02:45 | 0 | 0 | 0 | 10.1 | 0 | 1.531
2019-06-14 03:00 | 0 | 0 | 0 | 10.099 | 0 | 1.541
2019-06-14 03:15 | 0 | 0 | 0 | 10.087 | 0 | 1.523
2019-06-14 03:30 | 0 | 0 | 0 | 10.105 | 0 | 1.53
2019-06-14 03:45 | 0 | 0 | 0 | 10.108 | 0 | 1.526
2019-06-14 04:00 | 0 | 0 | 0 | 10.105 | 0 | 1.535
2019-06-14 04:15 | 0 | 0 | 0 | 10.095 | 0 | 1.534
2019-06-14 04:30 | 0 | 0 | 0 | 10.095 | 0 | 1.525
2019-06-14 04:45 | 0 | 0 | 0 | 10.11 | 0 | 1.526
2019-06-14 05:00 | 0 | 0 | 0 | 10.088 | 0 | 1.528
2019-06-14 05:15 | 0 | 0 | 0 | 10.09 | 0 | 1.522
2019-06-14 05:30 | 0 | 0 | 0 | 10.103 | 0 | 1.539
2019-06-14 05:45 | 0 | 0 | 0 | 10.103 | 0 | 1.534
2019-06-14 06:00 | 0 | 0 | 0 | 10.106 | 0 | 1.531
2019-06-14 06:15 | 0 | 0 | 0 | 10.085 | 0 | 1.539
2019-06-14 06:30 | 0 | 0 | 0 | 10.103 | 0 | 1.549
2019-06-14 06:45 | 0 | 0 | 0 | 10.102 | 0 | 1.545
2019-06-14 07:00 | 0 | 0 | 0 | 10.116 | 0 | 1.547
2019-06-14 07:15 | 0 | 0 | 0 | 10.103 | 0 | 1.539
2019-06-14 07:30 | 0 | 0 | 0 | 10.087 | 0 | 1.533
2019-06-14 07:45 | 0 | 0 | 0 | 10.092 | 0 | 1.552
2019-06-14 08:00 | 0 | 0 | 0 | 10.1 | 0 | 1.537
2019-06-14 08:15 | 0 | 0 | 0 | 10.105 | 0 | 1.543
2019-06-14 08:30 | 0 | 0 | 0 | 10.081 | 0 | 1.551
2019-06-14 08:45 | 0 | 0 | 0 | 10.085 | 0 | 1.537
2019-06-14 09:00 | 0 | 0 | 0 | 10.108 | 0 | 1.55 | 0.04 | 1.56 | 0
2019-06-14 09:15 | 0 | 0 | 0 | 10.094 | 0 | 1.553
2019-06-14 09:30 | 0 | 0 | 0 | 10.097 | 0 | 1.55
2019-06-14 09:45 | 0 | 0 | 0 | 10.118 | 0 | 1.545
2019-06-14 10:15 | 0 | 0 | 0 | 10.103 | 0 | 1.555
2019-06-14 10:30 | 0 | 0 | 0 | 10.085 | 0 | 1.541
2019-06-14 10:00 | 0 | 0 | 0 | 10.093 | 0 | 1.547
2019-06-14 10:45 | 0 | 0 | 0 | 10.098 | 0 | 1.556
2019-06-14 11:00 | 0 | 0 | 0 | 10.087 | 0 | 1.555
2019-06-14 11:15 | 0 | 0 | 0 | 10.099 | 0 | 1.549
2019-06-14 11:30 | 0 | 0 | 0 | 10.094 | 0 | 1.555
2019-06-14 11:45 | 0 | 0 | 0 | 10.091 | 0 | 1.567
2019-06-14 12:00 | 0 | 0 | 0 | 10.111 | 0 | 1.567
2019-06-14 12:30 | 0 | 0 | 0 | 10.094 | 0 | 1.546
2019-06-14 12:45 | 0 | 0 | 0 | 10.094 | 0 | 1.557
2019-06-14 13:00 | 0 | 0 | 0 | 10.094 | 0 | 1.564
2019-06-14 13:15 | 0 | 0 | 0 | 10.099 | 0 | 1.559
2019-06-14 13:30 | 0 | 0 | 0 | 10.094 | 0 | 1.558
2019-06-14 13:45 | 0 | 0 | 0 | 10.095 | 0 | 1.56
2019-06-14 14:00 | 0 | 0 | 0 | 10.091 | 0 | 1.562
2019-06-14 14:15 | 0 | 0 | 0 | 10.088 | 0 | 1.556
2019-06-14 14:30 | 0 | 0 | 0 | 10.097 | 0 | 1.557
2019-06-14 14:45 | 0 | 0 | 0 | 10.103 | 0 | 1.566
2019-06-14 15:00 | 0 | 0 | 0 | 10.111 | 0 | 1.569
2019-06-14 15:15 | 0 | 0 | 0 | 10.094 | 0 | 1.561
2019-06-14 15:30 | 0 | 0 | 0 | 10.097 | 0 | 1.577
2019-06-14 15:45 | 0 | 0 | 0 | 10.101 | 0 | 1.56
2019-06-14 16:00 | 0 | 0 | 0 | 10.106 | 0 | 1.58
2019-06-14 16:15 | 0 | 0 | 0 | 10.096 | 0 | 1.581
2019-06-14 16:30 | 0 | 0 | 0 | 10.117 | 0 | 1.565
2019-06-14 16:45 | 0 | 0 | 0 | 10.111 | 0 | 1.582
2019-06-14 17:00 | 0 | 0 | 0 | 10.099 | 0 | 1.57
2019-06-14 17:15 | 0 | 0 | 0 | 10.102 | 0 | 1.579
2019-06-14 17:30 | 0 | 0 | 0 | 10.085 | 0 | 1.582
2019-06-14 17:45 | 0 | 0 | 0 | 10.08 | 0 | 1.592
2019-06-14 18:00 | 0 | 0 | 0 | 10.109 | 0 | 1.578
2019-06-14 18:15 | 0 | 0 | 0 | 10.097 | 0 | 1.579
2019-06-14 18:30 | 0 | 0 | 0 | 10.102 | 0 | 1.579
2019-06-14 18:45 | 0 | 0 | 0 | 10.097 | 0 | 1.579
2019-06-14 19:00 | 0 | 0 | 0 | 10.097 | 0 | 1.592
2019-06-14 19:15 | 0 | 0 | 0 | 10.097 | 0 | 1.584
2019-06-14 19:30 | 0 | 0 | 0 | 10.086 | 0 | 1.587
2019-06-14 19:45 | 0 | 0 | 0 | 10.105 | 0 | 1.591
2019-06-14 20:00 | 0 | 0 | 0 | 10.112 | 0 | 1.59
2019-06-14 20:15 | 0 | 0 | 0 | 10.097 | 0 | 1.597
2019-06-14 20:30 | 0 | 0 | 0 | 10.118 | 0 | 1.595
2019-06-14 20:45 | 0 | 0 | 0 | 10.082 | 0 | 1.593
2019-06-14 21:00 | 0 | 0 | 0 | 10.091 | 0 | 1.59
2019-06-14 21:15 | 0 | 0 | 0 | 10.118 | 0 | 1.598
2019-06-14 21:30 | 0 | 0 | 0 | 10.078 | 0 | 1.608
2019-06-14 21:45 | 0 | 0 | 0 | 10.119 | 0 | 1.613
2019-06-14 22:00 | 0 | 0 | 0 | 10.105 | 0 | 1.608
2019-06-14 22:15 | 0 | 0 | 0 | 10.096 | 0 | 1.609
2019-06-14 22:30 | 0 | 0 | 0 | 10.103 | 0 | 1.61
2019-06-14 22:45 | 0 | 0 | 0 | 10.104 | 0 | 1.614
2019-06-14 23:00 | 0 | 0 | 0 | 10.094 | 0 | 1.619
2019-06-14 23:15 | 0 | 0 | 0 | 10.111 | 0 | 1.616
2019-06-14 23:30 | 0 | 0 | 0 | 10.111 | 0 | 1.606
2019-06-14 23:45 | 0 | 0 | 0 | 10.091 | 0 | 1.616
2019-06-15 | 0 | 0 | 0 | 10.097 | 0 | 1.607
2019-06-15 00:15 | 0 | 0 | 0 | 10.092 | 0 | 1.618
2019-06-15 00:30 | 0 | 0 | 0 | 10.097 | 0 | 1.617
2019-06-15 00:45 | 0 | 0 | 0 | 10.096 | 0 | 1.618
2019-06-15 01:00 | 0 | 0 | 0 | 10.096 | 0 | 1.624
2019-06-15 01:15 | 0 | 0 | 0 | 10.091 | 0 | 1.625
2019-06-15 01:30 | 0 | 0 | 0 | 10.109 | 0 | 1.624
2019-06-15 01:45 | 0 | 0 | 0 | 10.103 | 0 | 1.632
2019-06-15 02:00 | 0 | 0 | 0 | 10.106 | 0 | 1.618
2019-06-15 02:15 | 0 | 0 | 0 | 10.077 | 0 | 1.639
2019-06-15 02:30 | 0 | 0 | 0 | 10.091 | 0 | 1.637
2019-06-15 02:45 | 0 | 0 | 0 | 10.112 | 0 | 1.644
2019-06-15 03:00 | 0 | 0 | 0 | 10.111 | 0 | 1.621
2019-06-15 03:15 | 0 | 0 | 0 | 10.114 | 0 | 1.62
2019-06-15 03:30 | 0 | 0 | 0 | 10.1 | 0 | 1.626
2019-06-15 03:45 | 0 | 0 | 0 | 10.085 | 0 | 1.636
2019-06-15 04:00 | 0 | 0 | 0 | 10.104 | 0 | 1.633
2019-06-15 04:15 | 0 | 0 | 0 | 10.123 | 0 | 1.631
2019-06-15 04:30 | 0 | 0 | 0 | 10.094 | 0 | 1.638
2019-06-15 04:45 | 0 | 0 | 0 | 10.083 | 0 | 1.641
2019-06-15 05:00 | 0 | 0 | 0 | 10.121 | 0 | 1.632
2019-06-15 05:15 | 0 | 0 | 0 | 10.101 | 0 | 1.63
2019-06-15 05:30 | 0 | 0 | 0 | 10.097 | 0 | 1.639
2019-06-15 05:45 | 0 | 0 | 0 | 10.11 | 0 | 1.642
2019-06-15 06:00 | 0 | 0 | 0 | 10.086 | 0 | 1.643
2019-06-15 06:15 | 0 | 0 | 0 | 10.09 | 0 | 1.657
2019-06-15 06:30 | 0 | 0 | 0 | 10.111 | 0 | 1.637
2019-06-15 06:45 | 0 | 0 | 0 | 10.096 | 0 | 1.646
2019-06-15 07:00 | 0 | 0 | 0 | 10.104 | 0 | 1.64
2019-06-15 07:15 | 0 | 0 | 0 | 10.108 | 0 | 1.646
2019-06-15 07:30 | 0 | 0 | 0 | 10.089 | 0 | 1.658
2019-06-15 07:45 | 0 | 0 | 0 | 10.093 | 0 | 1.649
2019-06-15 08:00 | 0 | 0 | 0 | 10.108 | 0 | 1.655
2019-06-15 08:15 | 0 | 0 | 0 | 10.1 | 0 | 1.648
2019-06-15 08:30 | 0 | 0 | 0 | 10.094 | 0 | 1.646
2019-06-15 08:45 | 0 | 0 | 0 | 10.091 | 0 | 1.647
2019-06-15 09:00 | 0 | 0 | 0 | 10.099 | 0 | 1.661 | 0 | 1.64 | 0
2019-06-15 09:15 | 0 | 0 | 0 | 10.095 | 0 | 1.658
2019-06-15 09:30 | 0 | 0 | 0 | 10.097 | 0 | 1.662
2019-06-15 09:45 | 0 | 0 | 0 | 10.085 | 0 | 1.671
2019-06-15 10:00 | 116 | 1392 | 1.392 | 10.105 | 0 | 1.66
2019-06-15 10:15 | 161 | 1932 | 1.932 | 10.081 | 8.079 | 1.681
2019-06-15 10:30 | 155 | 1860 | 1.86 | 10.095 | 9.876 | 1.492
2019-06-15 10:45 | 148 | 1776 | 1.776 | 10.115 | 13.308 | 1.427
2019-06-15 11:00 | 145 | 1740 | 1.74 | 10.14 | 15.366 | 1.427
2019-06-15 11:15 | 142 | 1704 | 1.704 | 10.148 | 16.707 | 1.405
2019-06-15 11:30 | 140 | 1680 | 1.68 | 10.137 | 17.683 | 1.406
2019-06-15 11:45 | 139 | 1668 | 1.668 | 10.114 | 18.379 | 1.424
2019-06-15 12:00 | 138 | 1656 | 1.656 | 10.123 | 18.946 | 1.413
2019-06-15 12:15 | 137 | 1644 | 1.644 | 10.126 | 19.388 | 1.4
2019-06-15 12:30 | 137 | 1644 | 1.644 | 10.102 | 19.758 | 1.411
2019-06-15 12:45 | 137 | 1644 | 1.644 | 10.103 | 20.099 | 1.409
2019-06-15 13:00 | 137 | 1644 | 1.644 | 10.101 | 20.329 | 1.4
2019-06-15 13:15 | 135 | 1620 | 1.62 | 10.123 | 20.567 | 1.408
2019-06-15 13:30 | 136 | 1632 | 1.632 | 10.112 | 20.763 | 1.413
2019-06-15 13:45 | 136 | 1632 | 1.632 | 10.11 | 20.949 | 1.411
2019-06-15 14:00 | 135 | 1620 | 1.62 | 10.103 | 21.13 | 1.413
2019-06-15 14:15 | 136 | 1632 | 1.632 | 10.126 | 21.269 | 1.42
2019-06-15 14:30 | 135 | 1620 | 1.62 | 10.091 | 21.395 | 1.409
2019-06-15 14:45 | 135 | 1620 | 1.62 | 10.105 | 21.495 | 1.414
2019-06-15 15:00 | 135 | 1620 | 1.62 | 10.088 | 21.567 | 1.409
2019-06-15 15:15 | 135 | 1620 | 1.62 | 10.108 | 21.643 | 1.414
2019-06-15 15:30 | 134 | 1608 | 1.608 | 10.103 | 21.692 | 1.413
2019-06-15 15:45 | 135 | 1620 | 1.62 | 10.114 | 21.761 | 1.421
2019-06-15 16:00 | 134 | 1608 | 1.608 | 10.094 | 21.817 | 1.413
2019-06-15 16:15 | 134 | 1608 | 1.608 | 10.103 | 21.842 | 1.413
2019-06-15 16:30 | 134 | 1608 | 1.608 | 10.105 | 21.869 | 1.413
2019-06-15 16:45 | 134 | 1608 | 1.608 | 10.112 | 21.881 | 1.412
2019-06-15 17:00 | 134 | 1608 | 1.608 | 10.088 | 21.909 | 1.416
2019-06-15 17:15 | 134 | 1608 | 1.608 | 10.07 | 21.942 | 1.408
2019-06-15 17:30 | 134 | 1608 | 1.608 | 10.099 | 21.978 | 1.416
2019-06-15 17:45 | 133 | 1596 | 1.596 | 10.094 | 22.003 | 1.414
2019-06-15 18:00 | 133 | 1596 | 1.596 | 10.095 | 22.016 | 1.426
2019-06-15 18:15 | 133 | 1596 | 1.596 | 10.088 | 22.043 | 1.419
2019-06-15 18:30 | 134 | 1608 | 1.608 | 10.11 | 22.072 | 1.416
2019-06-15 18:45 | 134 | 1608 | 1.608 | 10.091 | 22.087 | 1.419
2019-06-15 19:00 | 134 | 1608 | 1.608 | 10.09 | 22.112 | 1.414
2019-06-15 19:15 | 133 | 1596 | 1.596 | 10.095 | 22.128 | 1.428
2019-06-15 19:30 | 133 | 1596 | 1.596 | 10.085 | 22.138 | 1.422
2019-06-15 19:45 | 134 | 1608 | 1.608 | 10.116 | 22.151 | 1.412
2019-06-15 20:00 | 133 | 1596 | 1.596 | 10.098 | 22.152 | 1.418
2019-06-15 20:15 | 134 | 1608 | 1.608 | 10.11 | 22.168 | 1.424
2019-06-15 20:30 | 134 | 1608 | 1.608 | 10.091 | 22.182 | 1.429
2019-06-15 20:45 | 133 | 1596 | 1.596 | 10.095 | 22.168 | 1.422
2019-06-15 21:00 | 133 | 1596 | 1.596 | 10.088 | 22.188 | 1.421
2019-06-15 21:15 | 133 | 1596 | 1.596 | 10.085 | 22.201 | 1.43
2019-06-15 21:30 | 133 | 1596 | 1.596 | 10.09 | 22.207 | 1.422
2019-06-15 21:45 | 133 | 1596 | 1.596 | 10.106 | 22.21 | 1.421
2019-06-15 22:00 | 133 | 1596 | 1.596 | 10.117 | 22.223 | 1.418
2019-06-15 22:15 | 133 | 1596 | 1.596 | 10.096 | 22.238 | 1.431
2019-06-15 22:30 | 133 | 1596 | 1.596 | 10.08 | 22.255 | 1.423
2019-06-15 22:45 | 134 | 1608 | 1.608 | 10.082 | 22.299 | 1.427
2019-06-15 23:00 | 131 | 1572 | 1.572 | 10.088 | 22.278 | 1.426
2019-06-15 23:15 | 132 | 1584 | 1.584 | 10.114 | 22.247 | 1.43
2019-06-15 23:30 | 133 | 1596 | 1.596 | 10.097 | 22.208 | 1.427
2019-06-15 23:45 | 132 | 1584 | 1.584 | 10.109 | 22.197 | 1.434
2019-06-16 | 132 | 1584 | 1.584 | 10.097 | 22.2 | 1.422
2019-06-16 00:15 | 132 | 1584 | 1.584 | 10.093 | 22.184 | 1.422
2019-06-16 00:30 | 132 | 1584 | 1.584 | 10.103 | 22.192 | 1.433
2019-06-16 00:45 | 132 | 1584 | 1.584 | 10.103 | 22.195 | 1.43
2019-06-16 01:00 | 132 | 1584 | 1.584 | 10.081 | 22.195 | 1.429
2019-06-16 01:15 | 133 | 1596 | 1.596 | 10.085 | 22.211 | 1.42
2019-06-16 01:30 | 133 | 1596 | 1.596 | 10.088 | 22.21 | 1.418
2019-06-16 01:45 | 132 | 1584 | 1.584 | 10.097 | 22.204 | 1.438
2019-06-16 02:00 | 132 | 1584 | 1.584 | 10.09 | 22.209 | 1.437
2019-06-16 02:15 | 132 | 1584 | 1.584 | 10.099 | 22.184 | 1.435
2019-06-16 02:30 | 132 | 1584 | 1.584 | 10.092 | 22.179 | 1.434
2019-06-16 02:45 | 132 | 1584 | 1.584 | 10.094 | 22.195 | 1.439
2019-06-16 03:00 | 132 | 1584 | 1.584 | 10.099 | 22.179 | 1.442
2019-06-16 03:15 | 132 | 1584 | 1.584 | 10.081 | 22.192 | 1.428
2019-06-16 03:30 | 133 | 1596 | 1.596 | 10.094 | 22.205 | 1.431
2019-06-16 03:45 | 132 | 1584 | 1.584 | 10.097 | 22.227 | 1.421
2019-06-16 04:00 | 132 | 1584 | 1.584 | 10.096 | 22.208 | 1.431
2019-06-16 04:15 | 132 | 1584 | 1.584 | 10.109 | 22.202 | 1.431
2019-06-16 04:30 | 133 | 1596 | 1.596 | 10.102 | 22.213 | 1.443
2019-06-16 04:45 | 132 | 1584 | 1.584 | 10.104 | 22.212 | 1.43
2019-06-16 05:00 | 132 | 1584 | 1.584 | 10.097 | 22.237 | 1.431
2019-06-16 05:15 | 132 | 1584 | 1.584 | 10.102 | 22.226 | 1.429
2019-06-16 05:30 | 133 | 1596 | 1.596 | 10.097 | 22.273 | 1.436
2019-06-16 05:45 | 132 | 1584 | 1.584 | 10.095 | 22.302 | 1.436
2019-06-16 06:00 | 132 | 1584 | 1.584 | 10.108 | 22.314 | 1.428
2019-06-16 06:15 | 132 | 1584 | 1.584 | 10.065 | 22.302 | 1.448
2019-06-16 06:30 | 133 | 1596 | 1.596 | 10.092 | 22.323 | 1.432
2019-06-16 06:45 | 133 | 1596 | 1.596 | 10.102 | 22.307 | 1.443
2019-06-16 07:00 | 132 | 1584 | 1.584 | 10.093 | 22.335 | 1.45
2019-06-16 07:15 | 133 | 1596 | 1.596 | 10.097 | 22.349 | 1.443
2019-06-16 07:30 | 133 | 1596 | 1.596 | 10.104 | 22.371 | 1.44
2019-06-16 07:45 | 133 | 1596 | 1.596 | 10.088 | 22.391 | 1.441
2019-06-16 08:00 | 132 | 1584 | 1.584 | 10.103 | 22.371 | 1.444
2019-06-16 08:15 | 133 | 1596 | 1.596 | 10.088 | 22.391 | 1.436
2019-06-16 08:30 | 132 | 1584 | 1.584 | 10.094 | 22.403 | 1.445
2019-06-16 08:45 | 133 | 1596 | 1.596 | 10.082 | 22.377 | 1.444
2019-06-16 09:00 | 132 | 1584 | 1.584 | 10.111 | 22.397 | 1.434 | 0.24
2019-06-16 09:15 | 132 | 1584 | 1.584 | 10.091 | 22.401 | 1.444
2019-06-16 09:30 | 133 | 1596 | 1.596 | 10.1 | 22.392 | 1.445
2019-06-16 09:45 | 132 | 1584 | 1.584 | 10.097 | 22.381 | 1.442
2019-06-16 10:00 | 132 | 1584 | 1.584 | 10.097 | 22.383 | 1.446
2019-06-16 10:15 | 132 | 1584 | 1.584 | 10.108 | 22.39 | 1.449
2019-06-16 10:30 | 133 | 1596 | 1.596 | 10.091 | 22.385 | 1.448
2019-06-16 10:45 | 133 | 1596 | 1.596 | 10.075 | 22.406 | 1.449
2019-06-16 11:00 | 132 | 1584 | 1.584 | 10.082 | 22.401 | 1.455
2019-06-16 11:15 | 133 | 1596 | 1.596 | 10.093 | 22.425 | 1.44
2019-06-16 11:30 | 132 | 1584 | 1.584 | 10.093 | 22.401 | 1.455
2019-06-16 11:45 | 132 | 1584 | 1.584 | 10.101 | 22.419 | 1.45
2019-06-16 12:00 | 132 | 1584 | 1.584 | 10.088 | 22.409 | 1.451
2019-06-16 12:15 | 132 | 1584 | 1.584 | 10.093 | 22.413 | 1.448
2019-06-16 12:30 | 132 | 1584 | 1.584 | 10.094 | 22.407 | 1.45
2019-06-16 12:45 | 132 | 1584 | 1.584 | 10.085 | 22.417 | 1.452
2019-06-16 13:00 | 132 | 1584 | 1.584 | 10.084 | 22.405 | 1.453
2019-06-16 13:15 | 133 | 1596 | 1.596 | 10.104 | 22.414 | 1.461
2019-06-16 13:30 | 132 | 1584 | 1.584 | 10.082 | 22.421 | 1.451
2019-06-16 13:45 | 132 | 1584 | 1.584 | 10.091 | 22.422 | 1.452
2019-06-16 14:00 | 133 | 1596 | 1.596 | 10.096 | 22.418 | 1.464
2019-06-16 14:15 | 133 | 1596 | 1.596 | 10.08 | 22.433 | 1.453
2019-06-16 14:30 | 132 | 1584 | 1.584 | 10.098 | 22.44 | 1.466
2019-06-16 14:45 | 132 | 1584 | 1.584 | 10.12 | 22.436 | 1.461
2019-06-16 15:00 | 133 | 1596 | 1.596 | 10.078 | 22.44 | 1.455
2019-06-16 15:15 | 133 | 1596 | 1.596 | 10.08 | 22.456 | 1.45
2019-06-16 15:30 | 132 | 1584 | 1.584 | 10.088 | 22.474 | 1.462
2019-06-16 15:45 | 133 | 1596 | 1.596 | 10.089 | 22.467 | 1.466
2019-06-16 16:00 | 132 | 1584 | 1.584 | 10.106 | 22.472 | 1.458
2019-06-16 16:15 | 132 | 1584 | 1.584 | 10.097 | 22.474 | 1.457
2019-06-16 16:30 | 132 | 1584 | 1.584 | 10.111 | 22.464 | 1.455
2019-06-16 16:45 | 132 | 1584 | 1.584 | 10.088 | 22.475 | 1.455
2019-06-16 17:00 | 132 | 1584 | 1.584 | 10.088 | 22.455 | 1.458
2019-06-16 17:15 | 132 | 1584 | 1.584 | 10.092 | 22.457 | 1.454
2019-06-16 17:30 | 132 | 1584 | 1.584 | 10.107 | 22.433 | 1.456
2019-06-16 17:45 | 132 | 1584 | 1.584 | 10.079 | 22.439 | 1.473
2019-06-16 18:00 | 132 | 1584 | 1.584 | 10.102 | 22.437 | 1.458
2019-06-16 18:15 | 131 | 1572 | 1.572 | 10.114 | 22.433 | 1.464
2019-06-16 18:30 | 132 | 1584 | 1.584 | 10.097 | 22.446 | 1.451
2019-06-16 18:45 | 132 | 1584 | 1.584 | 10.069 | 22.471 | 1.465
2019-06-16 19:00 | 132 | 1584 | 1.584 | 10.101 | 22.483 | 1.461
2019-06-16 19:15 | 132 | 1584 | 1.584 | 10.083 | 22.474 | 1.46
2019-06-16 19:30 | 133 | 1596 | 1.596 | 10.097 | 22.532 | 1.478
2019-06-16 19:45 | 133 | 1596 | 1.596 | 10.092 | 22.528 | 1.461
2019-06-16 20:00 | 133 | 1596 | 1.596 | 10.105 | 22.531 | 1.462
2019-06-16 20:15 | 133 | 1596 | 1.596 | 10.098 | 22.543 | 1.45
2019-06-16 20:30 | 133 | 1596 | 1.596 | 10.103 | 22.555 | 1.46
2019-06-16 20:45 | 132 | 1584 | 1.584 | 10.087 | 22.547 | 1.465
2019-06-16 21:00 | 132 | 1584 | 1.584 | 10.084 | 22.558 | 1.475
2019-06-16 21:15 | 132 | 1584 | 1.584 | 10.108 | 22.554 | 1.46
2019-06-16 21:30 | 132 | 1584 | 1.584 | 10.118 | 22.566 | 1.462
2019-06-16 21:45 | 132 | 1584 | 1.584 | 10.114 | 22.545 | 1.458
2019-06-16 22:00 | 132 | 1584 | 1.584 | 10.087 | 22.543 | 1.462
2019-06-16 22:15 | 132 | 1584 | 1.584 | 10.094 | 22.552 | 1.466
2019-06-16 22:30 | 132 | 1584 | 1.584 | 10.096 | 22.553 | 1.462
2019-06-16 22:45 | 132 | 1584 | 1.584 | 10.1 | 22.567 | 1.469
2019-06-16 23:00 | 132 | 1584 | 1.584 | 10.106 | 22.584 | 1.467
2019-06-16 23:15 | 132 | 1584 | 1.584 | 10.094 | 22.598 | 1.459
2019-06-16 23:30 | 133 | 1596 | 1.596 | 10.1 | 22.58 | 1.461
2019-06-16 23:45 | 132 | 1584 | 1.584 | 10.082 | 22.604 | 1.458
2019-06-17 | 132 | 1584 | 1.584 | 10.074 | 22.595 | 1.46
2019-06-17 00:15 | 132 | 1584 | 1.584 | 10.094 | 22.585 | 1.467
2019-06-17 00:30 | 132 | 1584 | 1.584 | 10.086 | 22.579 | 1.465
2019-06-17 00:45 | 132 | 1584 | 1.584 | 10.086 | 22.594 | 1.469
2019-06-17 01:00 | 132 | 1584 | 1.584 | 10.108 | 22.585 | 1.465
2019-06-17 01:15 | 132 | 1584 | 1.584 | 10.098 | 22.562 | 1.463
2019-06-17 01:30 | 132 | 1584 | 1.584 | 10.1 | 22.567 | 1.455
2019-06-17 01:45 | 132 | 1584 | 1.584 | 10.098 | 22.566 | 1.457
2019-06-17 02:00 | 131 | 1572 | 1.572 | 10.086 | 22.524 | 1.454
2019-06-17 02:15 | 132 | 1584 | 1.584 | 10.102 | 22.534 | 1.457
2019-06-17 02:30 | 132 | 1584 | 1.584 | 10.094 | 22.54 | 1.463
2019-06-17 02:45 | 132 | 1584 | 1.584 | 10.09 | 22.542 | 1.451
2019-06-17 03:00 | 132 | 1584 | 1.584 | 10.087 | 22.528 | 1.449
2019-06-17 03:15 | 132 | 1584 | 1.584 | 10.1 | 22.529 | 1.45
2019-06-17 03:30 | 132 | 1584 | 1.584 | 10.095 | 22.524 | 1.448
2019-06-17 03:45 | 132 | 1584 | 1.584 | 10.108 | 22.539 | 1.467
2019-06-17 04:00 | 132 | 1584 | 1.584 | 10.088 | 22.54 | 1.463
2019-06-17 04:15 | 131 | 1572 | 1.572 | 10.103 | 22.532 | 1.464
2019-06-17 04:30 | 132 | 1584 | 1.584 | 10.081 | 22.532 | 1.465
2019-06-17 04:45 | 132 | 1584 | 1.584 | 10.076 | 22.553 | 1.459
2019-06-17 05:00 | 131 | 1572 | 1.572 | 10.076 | 22.55 | 1.461
2019-06-17 05:15 | 133 | 1596 | 1.596 | 10.085 | 22.56 | 1.46
2019-06-17 05:30 | 132 | 1584 | 1.584 | 10.086 | 22.582 | 1.466
2019-06-17 05:45 | 132 | 1584 | 1.584 | 10.101 | 22.567 | 1.458
2019-06-17 06:00 | 132 | 1584 | 1.584 | 10.095 | 22.571 | 1.457
2019-06-17 06:15 | 132 | 1584 | 1.584 | 10.102 | 22.573 | 1.464
2019-06-17 06:30 | 132 | 1584 | 1.584 | 10.083 | 22.569 | 1.473
2019-06-17 06:45 | 131 | 1572 | 1.572 | 10.097 | 22.566 | 1.462
2019-06-17 07:00 | 132 | 1584 | 1.584 | 10.103 | 22.562 | 1.47
2019-06-17 07:15 | 132 | 1584 | 1.584 | 10.094 | 22.557 | 1.462
2019-06-17 07:30 | 131 | 1572 | 1.572 | 10.088 | 22.525 | 1.475
2019-06-17 07:45 | 132 | 1584 | 1.584 | 10.068 | 22.514 | 1.462
2019-06-17 08:00 | 132 | 1584 | 1.584 | 10.094 | 22.503 | 1.46
2019-06-17 08:15 | 130 | 1560 | 1.56 | 10.1 | 22.534 | 1.655
2019-06-17 08:30 | 0 | 0 | 0 | 10.092 | 22.73 | 1.68
2019-06-17 08:45 | 0 | 0 | 0 | 10.098 | 16.466 | 1.712
2019-06-17 09:00 | 0 | 0 | 0 | 10.108 | 12.362 | 1.708 | 0.29 | 1.45 | 22.77
2019-06-17 09:15 | 0 | 0 | 0 | 10.092 | 9.259 | 1.72
2019-06-17 09:30 | 0 | 0 | 0 | 10.094 | 6.991 | 1.718
2019-06-17 09:45 | 0 | 0 | 0 | 10.099 | 5.09 | 1.723
2019-06-17 10:00 | 0 | 0 | 0 | 10.1 | 3.831 | 1.711
2019-06-17 10:15 | 0 | 0 | 0 | 10.092 | 2.999 | 1.73
2019-06-17 10:30 | 0 | 0 | 0 | 10.103 | 2.42 | 1.709
2019-06-17 10:45 | 0 | 0 | 0 | 10.1 | 1.989 | 1.727
2019-06-17 11:00 | 0 | 0 | 0 | 10.11 | 1.72 | 1.73
2019-06-17 11:15 | 0 | 0 | 0 | 10.108 | 1.492 | 1.718
2019-06-17 11:30 | 0 | 0 | 0 | 10.103 | 1.32 | 1.729
2019-06-17 11:45 | 0 | 0 | 0 | 10.11 | 1.18 | 1.736
2019-06-17 12:00 | 0 | 0 | 0 | 10.109 | 1.048 | 1.723
2019-06-17 12:15 | 0 | 0 | 0 | 10.094 | 0.945 | 1.735
2019-06-17 12:30 | 0 | 0 | 0 | 10.089 | 0.849 | 1.727
2019-06-17 12:45 | 0 | 0 | 0 | 10.107 | 0.791 | 1.735
2019-06-17 13:00 | 0 | 0 | 0 | 10.094 | 0.714 | 1.728
2019-06-17 13:15 | 0 | 0 | 0 | 10.086 | 0.671 | 1.731
2019-06-17 13:30 | 0 | 0 | 0 | 10.085 | 0.64 | 1.743
2019-06-17 13:45 | 0 | 0 | 0 | 10.078 | 0.6 | 1.727
2019-06-17 14:00 | 0 | 0 | 0 | 10.086 | 0.556 | 1.719
2019-06-17 14:15 | 0 | 0 | 0 | 10.09 | 0.51 | 1.721
2019-06-17 14:30 | 0 | 0 | 0 | 10.102 | 0.493 | 1.735
2019-06-17 14:45 | 0 | 0 | 0 | 10.088 | 0.471 | 1.742
2019-06-17 15:00 | 0 | 0 | 0 | 10.103 | 0.454 | 1.739
2019-06-17 15:15 | 0 | 0 | 0 | 10.092 | 0.424 | 1.738
2019-06-17 15:30 | 0 | 0 | 0 | 10.086 | 0.406 | 1.734
2019-06-17 15:45 | 0 | 0 | 0 | 10.069 | 0.39 | 1.725
2019-06-17 16:00 | 0 | 0 | 0 | 10.078 | 0.365 | 1.738
2019-06-17 16:15 | 0 | 0 | 0 | 10.097 | 0.364 | 1.742
2019-06-17 16:30 | 0 | 0 | 0 | 10.085 | 0.341 | 1.737
2019-06-17 16:45 | 0 | 0 | 0 | 10.106 | 0.329 | 1.752
2019-06-17 17:00 | 0 | 0 | 0 | 10.094 | 0.331 | 1.744
2019-06-17 17:15 | 0 | 0 | 0 | 10.107 | 0.305 | 1.742
2019-06-17 17:30 | 0 | 0 | 0 | 10.099 | 0.303 | 1.742
2019-06-17 17:45 | 0 | 0 | 0 | 10.102 | 0.281 | 1.737
2019-06-17 18:00 | 0 | 0 | 0 | 10.085 | 0.28 | 1.731
2019-06-17 18:15 | 0 | 0 | 0 | 10.109 | 0.281 | 1.743
2019-06-17 18:30 | 0 | 0 | 0 | 10.097 | 0.267 | 1.749
2019-06-17 18:45 | 0 | 0 | 0 | 10.091 | 0.253 | 1.755
2019-06-17 19:00 | 0 | 0 | 0 | 10.119 | 0.256 | 1.741
2019-06-17 19:15 | 0 | 0 | 0 | 10.075 | 0.228 | 1.747
2019-06-17 19:30 | 0 | 0 | 0 | 10.098 | 0.234 | 1.737
2019-06-17 19:45 | 0 | 0 | 0 | 10.088 | 0.244 | 1.756
2019-06-17 20:00 | 0 | 0 | 0 | 10.091 | 0.243 | 1.755
2019-06-17 20:15 | 0 | 0 | 0 | 10.102 | 0.231 | 1.752
2019-06-17 20:30 | 0 | 0 | 0 | 10.103 | 0.228 | 1.763
2019-06-17 20:45 | 0 | 0 | 0 | 10.093 | 0.215 | 1.743
2019-06-17 21:00 | 0 | 0 | 0 | 10.083 | 0.213 | 1.755
2019-06-17 21:15 | 0 | 0 | 0 | 10.072 | 0.206 | 1.746
2019-06-17 21:30 | 0 | 0 | 0 | 10.114 | 0.208 | 1.754
2019-06-17 21:45 | 0 | 0 | 0 | 10.099 | 0.212 | 1.745
2019-06-17 22:00 | 0 | 0 | 0 | 10.083 | 0.213 | 1.743
2019-06-17 22:15 | 0 | 0 | 0 | 10.085 | 0.213 | 1.752
2019-06-17 22:30 | 0 | 0 | 0 | 10.079 | 0.197 | 1.746
2019-06-17 22:45 | 0 | 0 | 0 | 10.115 | 0.21 | 1.751
2019-06-17 23:00 | 0 | 0 | 0 | 10.082 | 0.215 | 1.747
2019-06-17 23:15 | 0 | 0 | 0 | 10.096 | 0.188 | 1.761
2019-06-17 23:30 | 0 | 0 | 0 | 10.101 | 0.205 | 1.763
2019-06-17 23:45 | 0 | 0 | 0 | 10.097 | 0.194 | 1.757
2019-06-18 | 0 | 0 | 0 | 10.111 | 0.187 | 1.749
2019-06-18 00:15 | 0 | 0 | 0 | 10.094 | 0.212 | 1.764
2019-06-18 00:30 | 0 | 0 | 0 | 10.091 | 0.19 | 1.754
2019-06-18 00:45 | 0 | 0 | 0 | 10.08 | 0.182 | 1.749
2019-06-18 01:00 | 0 | 0 | 0 | 10.111 | 0.202 | 1.763
2019-06-18 01:15 | 0 | 0 | 0 | 10.088 | 0.173 | 1.762
2019-06-18 01:30 | 0 | 0 | 0 | 10.089 | 0.179 | 1.765
2019-06-18 01:45 | 0 | 0 | 0 | 10.081 | 0.171 | 1.756
2019-06-18 02:00 | 0 | 0 | 0 | 10.096 | 0.182 | 1.767
2019-06-18 02:15 | 0 | 0 | 0 | 10.089 | 0.165 | 1.765
2019-06-18 02:30 | 0 | 0 | 0 | 10.105 | 0.163 | 1.763
2019-06-18 02:45 | 0 | 0 | 0 | 10.111 | 0.184 | 1.758
2019-06-18 03:00 | 0 | 0 | 0 | 10.087 | 0.185 | 1.754
2019-06-18 03:15 | 0 | 0 | 0 | 10.114 | 0.169 | 1.756
2019-06-18 03:30 | 0 | 0 | 0 | 10.097 | 0.182 | 1.763
2019-06-18 03:45 | 0 | 0 | 0 | 10.082 | 0.17 | 1.759
2019-06-18 04:00 | 0 | 0 | 0 | 10.097 | 0.161 | 1.771
2019-06-18 04:15 | 0 | 0 | 0 | 10.091 | 0.183 | 1.768
2019-06-18 04:30 | 0 | 0 | 0 | 10.084 | 0.154 | 1.756
2019-06-18 04:45 | 0 | 0 | 0 | 10.104 | 0.163 | 1.768
2019-06-18 05:00 | 0 | 0 | 0 | 10.082 | 0.174 | 1.772
2019-06-18 05:15 | 0 | 0 | 0 | 10.082 | 0.16 | 1.759
2019-06-18 05:30 | 0 | 0 | 0 | 10.111 | 0.156 | 1.76
2019-06-18 05:45 | 0 | 0 | 0 | 10.098 | 0.164 | 1.757
2019-06-18 06:00 | 0 | 0 | 0 | 10.09 | 0.155 | 1.756
2019-06-18 06:15 | 0 | 0 | 0 | 10.107 | 0.164 | 1.756
2019-06-18 06:30 | 0 | 0 | 0 | 10.095 | 0.15 | 1.764
2019-06-18 06:45 | 0 | 0 | 0 | 10.095 | 0.173 | 1.769
2019-06-18 07:00 | 0 | 0 | 0 | 10.09 | 0.164 | 1.759
2019-06-18 07:15 | 0 | 0 | 0 | 10.103 | 0.161 | 1.766
2019-06-18 07:30 | 0 | 0 | 0 | 10.091 | 0.154 | 1.765
2019-06-18 07:45 | 0 | 0 | 0 | 10.1 | 0.164 | 1.755
2019-06-18 08:00 | 0 | 0 | 0 | 10.108 | 0.148 | 1.763
2019-06-18 08:15 | 0 | 0 | 0 | 10.086 | 0.172 | 1.767
2019-06-18 08:30 | 0 | 0 | 0 | 10.087 | 0.155 | 1.768
2019-06-18 08:45 | 0 | 0 | 0 | 10.084 | 0.17 | 1.769
2019-06-18 09:00 | 0 | 0 | 0 | 10.094 | 0.167 | 1.769 | 0.37 | 1.76 | 0.145
2019-06-18 09:15 | 0 | 0 | 0 | 10.079 | 0.174 | 1.774
2019-06-18 09:30 | 0 | 0 | 0 | 10.076 | 0.169 | 1.761
2019-06-18 09:45 | 0 | 0 | 0 | 10.086 | 0.18 | 1.762
2019-06-18 10:00 | 0 | 0 | 0 | 10.09 | 0.172 | 1.78
2019-06-18 10:15 | 0 | 0 | 0 | 10.068 | 0.179 | 1.765
2019-06-18 10:30 | 0 | 0 | 0 | 10.091 | 0.174 | 1.78
2019-06-18 10:45 | 0 | 0 | 0 | 10.108 | 0.184 | 1.764
2019-06-18 11:00 | 0 | 0 | 0 | 10.098 | 0.173 | 1.787
2019-06-18 11:15 | 0 | 0 | 0 | 10.103 | 0.185 | 1.769
2019-06-18 11:30 | 0 | 0 | 0 | 10.097 | 0.176 | 1.758
2019-06-18 11:45 | 0 | 0 | 0 | 10.101 | 0.165 | 1.776
2019-06-18 12:00 | 0 | 0 | 0 | 10.085 | 0.179 | 1.768
2019-06-18 12:15 | 0 | 0 | 0 | 10.113 | 0.178 | 1.767
2019-06-18 12:30 | 0 | 0 | 0 | 10.096 | 0.167 | 1.771
2019-06-18 12:45 | 0 | 0 | 0 | 10.1 | 0.155 | 1.772
2019-06-18 13:00 | 0 | 0 | 0 | 10.089 | 0.169 | 1.774
2019-06-18 13:15 | 0 | 0 | 0 | 10.091 | 0.158 | 1.779
2019-06-18 13:30 | 0 | 0 | 0 | 10.088 | 0.179 | 1.782
2019-06-18 13:45 | 0 | 0 | 0 | 10.105 | 0.163 | 1.789
2019-06-18 14:00 | 0 | 0 | 0 | 10.111 | 0.158 | 1.785
2019-06-18 14:15 | 0 | 0 | 0 | 10.092 | 0.147 | 1.778
2019-06-18 14:30 | 0 | 0 | 0 | 10.088 | 0.164 | 1.79
2019-06-18 14:45 | 0 | 0 | 0 | 10.077 | 0.145 | 1.782
2019-06-18 15:00 | 0 | 0 | 0 | 10.094 | 0.146 | 1.787
2019-06-18 15:15 | 0 | 0 | 0 | 10.1 | 0.155 | 1.772
2019-06-18 15:30 | 0 | 0 | 0 | 10.103 | 0.147 | 1.786
2019-06-18 15:45 | 0 | 0 | 0 | 10.094 | 0.156 | 1.772
2019-06-18 16:00 | 0 | 0 | 0 | 10.105 | 0.124 | 1.771
2019-06-18 16:15 | 0 | 0 | 0 | 10.091 | 0.138 | 1.772
2019-06-18 16:30 | 0 | 0 | 0 | 10.081 | 0.151 | 1.776
2019-06-18 16:45 | 0 | 0 | 0 | 10.088 | 0.142 | 1.776
2019-06-18 17:00 | 0 | 0 | 0 | 10.101 | 0.137 | 1.778
2019-06-18 17:15 | 0 | 0 | 0 | 10.12 | 0.136 | 1.785
2019-06-18 17:30 | 0 | 0 | 0 | 10.088 | 0.137 | 1.793
2019-06-18 17:45 | 0 | 0 | 0 | 10.1 | 0.123 | 1.785
2019-06-18 18:00 | 0 | 0 | 0 | 10.105 | 0.138 | 1.779
2019-06-18 18:15 | 0 | 0 | 0 | 10.081 | 0.141 | 1.78
2019-06-18 18:30 | 0 | 0 | 0 | 10.105 | 0.126 | 1.777
2019-06-18 18:45 | 0 | 0 | 0 | 10.08 | 0.141 | 1.789
2019-06-18 19:00 | 0 | 0 | 0 | 10.094 | 0.143 | 1.785
2019-06-18 19:15 | 0 | 0 | 0 | 10.085 | 0.151 | 1.795
2019-06-18 19:30 | 0 | 0 | 0 | 10.077 | 0.133 | 1.781
2019-06-18 19:45 | 0 | 0 | 0 | 10.111 | 0.137 | 1.781
2019-06-18 20:00 | 0 | 0 | 0 | 10.089 | 0.143 | 1.793
2019-06-18 20:15 | 0 | 0 | 0 | 10.091 | 0.153 | 1.772
2019-06-18 20:30 | 0 | 0 | 0 | 10.107 | 0.142 | 1.785
2019-06-18 20:45 | 0 | 0 | 0 | 10.097 | 0.132 | 1.785
2019-06-18 21:00 | 0 | 0 | 0 | 10.094 | 0.143 | 1.802
2019-06-18 21:15 | 0 | 0 | 0 | 10.091 | 0.129 | 1.78
2019-06-18 21:30 | 0 | 0 | 0 | 10.105 | 0.139 | 1.786
2019-06-18 21:45 | 0 | 0 | 0 | 10.089 | 0.141 | 1.787
2019-06-18 22:00 | 0 | 0 | 0 | 10.083 | 0.142 | 1.795
2019-06-18 22:15 | 0 | 0 | 0 | 10.086 | 0.138 | 1.791
2019-06-18 22:30 | 0 | 0 | 0 | 10.084 | 0.144 | 1.779
2019-06-18 22:45 | 0 | 0 | 0 | 10.093 | 0.153 | 1.784
2019-06-18 23:00 | 0 | 0 | 0 | 10.088 | 0.15 | 1.772
2019-06-18 23:15 | 0 | 0 | 0 | 10.093 | 0.156 | 1.778
2019-06-18 23:30 | 0 | 0 | 0 | 10.083 | 0.155 | 1.79
2019-06-18 23:45 | 0 | 0 | 0 | 10.088 | 0.15 | 1.797
2019-06-19 | 0 | 0 | 0 | 10.091 | 0.163 | 1.792
2019-06-19 00:15 | 0 | 0 | 0 | 10.105 | 0.151 | 1.785
2019-06-19 00:30 | 0 | 0 | 0 | 10.103 | 0.156 | 1.794
2019-06-19 00:45 | 0 | 0 | 0 | 10.098 | 0.163 | 1.789
2019-06-19 01:00 | 0 | 0 | 0 | 10.094 | 0.144 | 1.791
2019-06-19 01:15 | 0 | 0 | 0 | 10.083 | 0.147 | 1.783
2019-06-19 01:30 | 0 | 0 | 0 | 10.1 | 0.162 | 1.792
2019-06-19 01:45 | 0 | 0 | 0 | 10.109 | 0.162 | 1.81
2019-06-19 02:00 | 0 | 0 | 0 | 10.091 | 0.158 | 1.8
2019-06-19 02:15 | 0 | 0 | 0 | 10.103 | 0.153 | 1.789
2019-06-19 02:30 | 0 | 0 | 0 | 10.091 | 0.164 | 1.801
2019-06-19 02:45 | 0 | 0 | 0 | 10.078 | 0.154 | 1.8
2019-06-19 03:00 | 0 | 0 | 0 | 10.101 | 0.151 | 1.802
2019-06-19 03:15 | 0 | 0 | 0 | 10.106 | 0.147 | 1.794
2019-06-19 03:30 | 0 | 0 | 0 | 10.101 | 0.148 | 1.799
2019-06-19 03:45 | 0 | 0 | 0 | 10.099 | 0.145 | 1.809
2019-06-19 04:00 | 0 | 0 | 0 | 10.12 | 0.152 | 1.793
2019-06-19 04:15 | 0 | 0 | 0 | 10.111 | 0.168 | 1.804
2019-06-19 04:30 | 0 | 0 | 0 | 10.096 | 0.155 | 1.8
2019-06-19 04:45 | 0 | 0 | 0 | 10.094 | 0.147 | 1.796
2019-06-19 05:00 | 0 | 0 | 0 | 10.094 | 0.144 | 1.786
2019-06-19 05:15 | 0 | 0 | 0 | 10.095 | 0.146 | 1.799
2019-06-19 05:30 | 0 | 0 | 0 | 10.097 | 0.16 | 1.798
2019-06-19 05:45 | 0 | 0 | 0 | 10.109 | 0.154 | 1.812
2019-06-19 06:00 | 0 | 0 | 0 | 10.079 | 0.153 | 1.797
2019-06-19 06:15 | 0 | 0 | 0 | 10.093 | 0.153 | 1.808
2019-06-19 06:30 | 0 | 0 | 0 | 10.104 | 0.152 | 1.805
2019-06-19 06:45 | 0 | 0 | 0 | 10.085 | 0.156 | 1.798
2019-06-19 07:00 | 0 | 0 | 0 | 10.104 | 0.167 | 1.794
2019-06-19 07:15 | 0 | 0 | 0 | 10.089 | 0.163 | 1.806
2019-06-19 07:30 | 0 | 0 | 0 | 10.097 | 0.167 | 1.799
2019-06-19 07:45 | 0 | 0 | 0 | 10.094 | 0.159 | 1.809
2019-06-19 08:00 | 0 | 0 | 0 | 10.098 | 0.155 | 1.803
2019-06-19 08:15 | 0 | 0 | 0 | 10.085 | 0.183 | 1.812
2019-06-19 08:30 | 132 | 1584 | 1.584 | 10.093 | 6.045 | 1.808
2019-06-19 08:45 | 142 | 1704 | 1.704 | 10.117 | 10.082 | 1.803
2019-06-19 09:00 | 138 | 1656 | 1.656 | 10.131 | 12.723 | 1.631 | 0.93 | 1.19 | 0.14
2019-06-19 09:15 | 133 | 1596 | 1.596 | 10.146 | 14.58 | 1.709
2019-06-19 09:30 | 131 | 1572 | 1.572 | 10.134 | 15.715 | 1.698
2019-06-19 09:45 | 130 | 1560 | 1.56 | 10.137 | 16.532 | 1.701
2019-06-19 10:00 | 129 | 1548 | 1.548 | 10.127 | 17.125 | 1.691
2019-06-19 10:15 | 129 | 1548 | 1.548 | 10.125 | 17.62 | 1.69
2019-06-19 10:30 | 129 | 1548 | 1.548 | 10.114 | 18.023 | 1.695
2019-06-19 10:45 | 128 | 1536 | 1.536 | 10.11 | 18.328 | 1.697
2019-06-19 11:00 | 127 | 1524 | 1.524 | 10.121 | 18.563 | 1.706
2019-06-19 11:15 | 127 | 1524 | 1.524 | 10.12 | 18.73 | 1.72
2019-06-19 11:30 | 126 | 1512 | 1.512 | 10.091 | 18.825 | 1.706
2019-06-19 11:45 | 126 | 1512 | 1.512 | 10.091 | 18.944 | 1.704
2019-06-19 12:00 | 126 | 1512 | 1.512 | 10.096 | 19.031 | 1.696
2019-06-19 12:15 | 124 | 1488 | 1.488 | 10.103 | 19.099 | 1.7
2019-06-19 12:30 | 124 | 1488 | 1.488 | 10.105 | 19.059 | 1.709
2019-06-19 12:45 | 124 | 1488 | 1.488 | 10.098 | 19.072 | 1.712
2019-06-19 13:00 | 124 | 1488 | 1.488 | 10.089 | 19.084 | 1.698
2019-06-19 13:15 | 123 | 1476 | 1.476 | 10.101 | 19.098 | 1.706
2019-06-19 13:30 | 124 | 1488 | 1.488 | 10.117 | 19.119 | 1.711
2019-06-19 13:45 | 124 | 1488 | 1.488 | 10.108 | 19.126 | 1.701
2019-06-19 14:00 | 124 | 1488 | 1.488 | 10.101 | 19.165 | 1.706
2019-06-19 14:15 | 124 | 1488 | 1.488 | 10.117 | 19.175 | 1.695
2019-06-19 14:30 | 124 | 1488 | 1.488 | 10.088 | 19.209 | 1.702
2019-06-19 14:45 | 124 | 1488 | 1.488 | 10.091 | 19.21 | 1.711
2019-06-19 15:00 | 124 | 1488 | 1.488 | 10.091 | 19.238 | 1.712
2019-06-19 15:15 | 124 | 1488 | 1.488 | 10.075 | 19.278 | 1.71
2019-06-19 15:30 | 124 | 1488 | 1.488 | 10.095 | 19.275 | 1.699
2019-06-19 15:45 | 124 | 1488 | 1.488 | 10.118 | 19.27 | 1.707
2019-06-19 16:00 | 123 | 1476 | 1.476 | 10.102 | 19.298 | 1.714
2019-06-19 16:15 | 124 | 1488 | 1.488 | 10.079 | 19.29 | 1.703
2019-06-19 16:30 | 124 | 1488 | 1.488 | 10.102 | 19.32 | 1.728
2019-06-19 16:45 | 124 | 1488 | 1.488 | 10.097 | 19.339 | 1.715
2019-06-19 17:00 | 123 | 1476 | 1.476 | 10.099 | 19.346 | 1.712
2019-06-19 17:15 | 125 | 1500 | 1.5 | 10.103 | 19.359 | 1.708
2019-06-19 17:30 | 124 | 1488 | 1.488 | 10.087 | 19.4 | 1.699
2019-06-19 17:45 | 124 | 1488 | 1.488 | 10.098 | 19.401 | 1.709
2019-06-19 18:00 | 124 | 1488 | 1.488 | 10.091 | 19.41 | 1.705
2019-06-19 18:15 | 124 | 1488 | 1.488 | 10.08 | 19.422 | 1.711
2019-06-19 18:30 | 124 | 1488 | 1.488 | 10.088 | 19.44 | 1.719
2019-06-19 18:45 | 124 | 1488 | 1.488 | 10.1 | 19.454 | 1.72
2019-06-19 19:00 | 123 | 1476 | 1.476 | 10.088 | 19.448 | 1.718
2019-06-19 19:15 | 124 | 1488 | 1.488 | 10.093 | 19.457 | 1.713
2019-06-19 19:30 | 124 | 1488 | 1.488 | 10.094 | 19.45 | 1.716
2019-06-19 19:45 | 125 | 1500 | 1.5 | 10.097 | 19.474 | 1.718
2019-06-19 20:00 | 124 | 1488 | 1.488 | 10.094 | 19.496 | 1.714
2019-06-19 20:15 | 124 | 1488 | 1.488 | 10.085 | 19.503 | 1.717
2019-06-19 20:30 | 124 | 1488 | 1.488 | 10.1 | 19.5 | 1.719
2019-06-19 20:45 | 124 | 1488 | 1.488 | 10.1 | 19.509 | 1.72
2019-06-19 21:00 | 124 | 1488 | 1.488 | 10.091 | 19.498 | 1.721
2019-06-19 21:15 | 122 | 1464 | 1.464 | 10.085 | 19.504 | 1.737
2019-06-19 21:30 | 121 | 1452 | 1.452 | 10.093 | 19.397 | 1.71
2019-06-19 21:45 | 122 | 1464 | 1.464 | 10.097 | 19.351 | 1.72
2019-06-19 22:00 | 122 | 1464 | 1.464 | 10.114 | 19.305 | 1.709
2019-06-19 22:15 | 121 | 1452 | 1.452 | 10.102 | 19.29 | 1.731
2019-06-19 22:30 | 122 | 1464 | 1.464 | 10.103 | 19.283 | 1.709
2019-06-19 22:45 | 122 | 1464 | 1.464 | 10.099 | 19.281 | 1.713
2019-06-19 23:00 | 122 | 1464 | 1.464 | 10.092 | 19.26 | 1.723
2019-06-19 23:15 | 121 | 1452 | 1.452 | 10.094 | 19.254 | 1.726
2019-06-19 23:30 | 122 | 1464 | 1.464 | 10.104 | 19.265 | 1.738
2019-06-19 23:45 | 122 | 1464 | 1.464 | 10.101 | 19.229 | 1.728
2019-06-20 | 122 | 1464 | 1.464 | 10.091 | 19.253 | 1.718
2019-06-20 00:15 | 122 | 1464 | 1.464 | 10.083 | 19.253 | 1.724
2019-06-20 00:30 | 122 | 1464 | 1.464 | 10.1 | 19.266 | 1.72
2019-06-20 00:45 | 122 | 1464 | 1.464 | 10.098 | 19.272 | 1.722
2019-06-20 01:00 | 122 | 1464 | 1.464 | 10.101 | 19.285 | 1.733
2019-06-20 01:15 | 122 | 1464 | 1.464 | 10.081 | 19.275 | 1.731
2019-06-20 01:30 | 122 | 1464 | 1.464 | 10.094 | 19.292 | 1.725
2019-06-20 01:45 | 122 | 1464 | 1.464 | 10.112 | 19.292 | 1.729
2019-06-20 02:00 | 122 | 1464 | 1.464 | 10.094 | 19.279 | 1.731
2019-06-20 02:15 | 122 | 1464 | 1.464 | 10.114 | 19.308 | 1.729
2019-06-20 02:30 | 122 | 1464 | 1.464 | 10.088 | 19.301 | 1.746
2019-06-20 02:45 | 122 | 1464 | 1.464 | 10.087 | 19.281 | 1.724
2019-06-20 03:00 | 121 | 1452 | 1.452 | 10.091 | 19.258 | 1.727
2019-06-20 03:15 | 121 | 1452 | 1.452 | 10.08 | 19.237 | 1.728
2019-06-20 03:30 | 121 | 1452 | 1.452 | 10.088 | 19.222 | 1.727
2019-06-20 03:45 | 121 | 1452 | 1.452 | 10.097 | 19.233 | 1.729
2019-06-20 04:00 | 121 | 1452 | 1.452 | 10.091 | 19.235 | 1.721
2019-06-20 04:15 | 121 | 1452 | 1.452 | 10.085 | 19.214 | 1.73
2019-06-20 04:30 | 122 | 1464 | 1.464 | 10.103 | 19.216 | 1.742
2019-06-20 04:45 | 122 | 1464 | 1.464 | 10.093 | 19.242 | 1.735
2019-06-20 05:00 | 122 | 1464 | 1.464 | 10.096 | 19.265 | 1.733
2019-06-20 05:15 | 122 | 1464 | 1.464 | 10.099 | 19.235 | 1.739
2019-06-20 05:30 | 121 | 1452 | 1.452 | 10.105 | 19.236 | 1.734
2019-06-20 05:45 | 121 | 1452 | 1.452 | 10.083 | 19.224 | 1.741
2019-06-20 06:00 | 121 | 1452 | 1.452 | 10.094 | 19.218 | 1.746
2019-06-20 06:15 | 121 | 1452 | 1.452 | 10.094 | 19.222 | 1.731
2019-06-20 06:30 | 121 | 1452 | 1.452 | 10.086 | 19.218 | 1.736
2019-06-20 06:45 | 121 | 1452 | 1.452 | 10.089 | 19.222 | 1.723
2019-06-20 07:00 | 121 | 1452 | 1.452 | 10.096 | 19.205 | 1.745
2019-06-20 07:15 | 121 | 1452 | 1.452 | 10.094 | 19.186 | 1.731
2019-06-20 07:30 | 121 | 1452 | 1.452 | 10.087 | 19.179 | 1.735
2019-06-20 07:45 | 125 | 1500 | 1.5 | 10.1 | 19.517 | 1.735
2019-06-20 08:00 | 142 | 1704 | 1.704 | 10.106 | 20.166 | 1.726
2019-06-20 08:15 | 140 | 1680 | 1.68 | 10.083 | 20.946 | 1.741
2019-06-20 08:30 | 140 | 1680 | 1.68 | 10.11 | 21.449 | 1.73
2019-06-20 08:45 | 139 | 1668 | 1.668 | 10.108 | 21.777 | 1.742
2019-06-20 09:00 | 139 | 1668 | 1.668 | 10.086 | 21.907 | 1.729 | 1.48 | 1.72 | 19.43
2019-06-20 09:15 | 138 | 1656 | 1.656 | 10.094 | 22.156 | 1.747
2019-06-20 09:30 | 138 | 1656 | 1.656 | 10.101 | 22.377 | 1.738
2019-06-20 09:45 | 137 | 1644 | 1.644 | 10.088 | 22.562 | 1.732
2019-06-20 10:00 | 137 | 1644 | 1.644 | 10.088 | 22.698 | 1.748
2019-06-20 10:15 | 137 | 1644 | 1.644 | 10.1 | 22.784 | 1.742
2019-06-20 10:30 | 136 | 1632 | 1.632 | 10.093 | 22.876 | 1.751
2019-06-20 10:45 | 136 | 1632 | 1.632 | 10.08 | 22.938 | 1.742
2019-06-20 11:00 | 136 | 1632 | 1.632 | 10.098 | 22.99 | 1.743
2019-06-20 11:15 | 136 | 1632 | 1.632 | 10.097 | 23.051 | 1.743
2019-06-20 11:30 | 137 | 1644 | 1.644 | 10.094 | 23.086 | 1.757
2019-06-20 11:45 | 137 | 1644 | 1.644 | 10.1 | 23.137 | 1.752
2019-06-20 12:00 | 136 | 1632 | 1.632 | 10.091 | 23.201 | 1.746
2019-06-20 12:15 | 136 | 1632 | 1.632 | 10.109 | 23.219 | 1.741
2019-06-20 12:30 | 136 | 1632 | 1.632 | 10.098 | 23.251 | 1.757
2019-06-20 12:45 | 136 | 1632 | 1.632 | 10.104 | 23.297 | 1.754
2019-06-20 13:00 | 136 | 1632 | 1.632 | 10.103 | 23.304 | 1.75
2019-06-20 13:15 | 136 | 1632 | 1.632 | 10.091 | 23.312 | 1.755
2019-06-20 13:30 | 136 | 1632 | 1.632 | 10.091 | 23.35 | 1.746
2019-06-20 13:45 | 136 | 1632 | 1.632 | 10.097 | 23.362 | 1.767
2019-06-20 14:00 | 135 | 1620 | 1.62 | 10.097 | 23.398 | 1.756
2019-06-20 14:15 | 136 | 1632 | 1.632 | 10.087 | 23.391 | 1.756
2019-06-20 14:30 | 135 | 1620 | 1.62 | 10.104 | 23.393 | 1.755
2019-06-20 14:45 | 137 | 1644 | 1.644 | 10.108 | 23.465 | 1.762
2019-06-20 15:00 | 136 | 1632 | 1.632 | 10.1 | 23.489 | 1.77
2019-06-20 15:15 | 136 | 1632 | 1.632 | 10.108 | 23.498 | 1.749
2019-06-20 15:30 | 136 | 1632 | 1.632 | 10.09 | 23.489 | 1.75
2019-06-20 15:45 | 136 | 1632 | 1.632 | 10.09 | 23.504 | 1.744
2019-06-20 16:00 | 135 | 1620 | 1.62 | 10.09 | 23.521 | 1.762
2019-06-20 16:15 | 136 | 1632 | 1.632 | 10.097 | 23.479 | 1.768
2019-06-20 16:30 | 136 | 1632 | 1.632 | 10.109 | 23.546 | 1.765
2019-06-20 16:45 | 136 | 1632 | 1.632 | 10.105 | 23.543 | 1.762
2019-06-20 17:00 | 136 | 1632 | 1.632 | 10.102 | 23.557 | 1.764
2019-06-20 17:15 | 136 | 1632 | 1.632 | 10.077 | 23.583 | 1.769
2019-06-20 17:30 | 136 | 1632 | 1.632 | 10.081 | 23.575 | 1.76
2019-06-20 17:45 | 136 | 1632 | 1.632 | 10.097 | 23.586 | 1.768
2019-06-20 18:00 | 136 | 1632 | 1.632 | 10.11 | 23.608 | 1.754
2019-06-20 18:15 | 136 | 1632 | 1.632 | 10.099 | 23.634 | 1.763
2019-06-20 18:30 | 136 | 1632 | 1.632 | 10.078 | 23.629 | 1.767
2019-06-20 18:45 | 136 | 1632 | 1.632 | 10.103 | 23.661 | 1.75
2019-06-20 19:00 | 136 | 1632 | 1.632 | 10.077 | 23.66 | 1.764
2019-06-20 19:15 | 135 | 1620 | 1.62 | 10.104 | 23.667 | 1.772
2019-06-20 19:30 | 136 | 1632 | 1.632 | 10.102 | 23.664 | 1.779
2019-06-20 19:45 | 136 | 1632 | 1.632 | 10.104 | 23.661 | 1.762
2019-06-20 20:00 | 136 | 1632 | 1.632 | 10.092 | 23.678 | 1.759
2019-06-20 20:15 | 137 | 1644 | 1.644 | 10.093 | 23.71 | 1.774
2019-06-20 20:30 | 136 | 1632 | 1.632 | 10.106 | 23.721 | 1.757
2019-06-20 20:45 | 135 | 1620 | 1.62 | 10.11 | 23.7 | 1.779
2019-06-20 21:00 | 135 | 1620 | 1.62 | 10.08 | 23.713 | 1.768
2019-06-20 21:15 | 136 | 1632 | 1.632 | 10.123 | 23.709 | 1.766
2019-06-20 21:30 | 136 | 1632 | 1.632 | 10.079 | 23.709 | 1.778
2019-06-20 21:45 | 136 | 1632 | 1.632 | 10.083 | 23.738 | 1.77
2019-06-20 22:00 | 136 | 1632 | 1.632 | 10.091 | 23.747 | 1.774
2019-06-20 22:15 | 136 | 1632 | 1.632 | 10.1 | 23.75 | 1.764
2019-06-20 22:30 | 136 | 1632 | 1.632 | 10.093 | 23.742 | 1.771
2019-06-20 22:45 | 136 | 1632 | 1.632 | 10.095 | 23.749 | 1.768
2019-06-20 23:00 | 135 | 1620 | 1.62 | 10.108 | 23.735 | 1.765
2019-06-20 23:15 | 136 | 1632 | 1.632 | 10.071 | 23.751 | 1.774
2019-06-20 23:30 | 135 | 1620 | 1.62 | 10.091 | 23.724 | 1.768
2019-06-20 23:45 | 135 | 1620 | 1.62 | 10.083 | 23.72 | 1.785
2019-06-21 | 135 | 1620 | 1.62 | 10.103 | 23.738 | 1.779
2019-06-21 00:15 | 136 | 1632 | 1.632 | 10.101 | 23.742 | 1.788
2019-06-21 00:30 | 136 | 1632 | 1.632 | 10.083 | 23.779 | 1.77
2019-06-21 00:45 | 135 | 1620 | 1.62 | 10.097 | 23.734 | 1.782
2019-06-21 01:00 | 136 | 1632 | 1.632 | 10.097 | 23.761 | 1.782
2019-06-21 01:15 | 136 | 1632 | 1.632 | 10.094 | 23.772 | 1.779
2019-06-21 01:30 | 136 | 1632 | 1.632 | 10.094 | 23.778 | 1.781
2019-06-21 01:45 | 135 | 1620 | 1.62 | 10.105 | 23.782 | 1.781
2019-06-21 02:00 | 136 | 1632 | 1.632 | 10.086 | 23.792 | 1.786
2019-06-21 02:15 | 135 | 1620 | 1.62 | 10.101 | 23.775 | 1.777
2019-06-21 02:30 | 136 | 1632 | 1.632 | 10.082 | 23.767 | 1.787
2019-06-21 02:45 | 136 | 1632 | 1.632 | 10.108 | 23.773 | 1.77
2019-06-21 03:00 | 135 | 1620 | 1.62 | 10.101 | 23.778 | 1.781
2019-06-21 03:15 | 136 | 1632 | 1.632 | 10.089 | 23.786 | 1.787
2019-06-21 03:30 | 136 | 1632 | 1.632 | 10.095 | 23.774 | 1.777
2019-06-21 03:45 | 135 | 1620 | 1.62 | 10.079 | 23.752 | 1.78
2019-06-21 04:00 | 135 | 1620 | 1.62 | 10.085 | 23.75 | 1.78
2019-06-21 04:15 | 135 | 1620 | 1.62 | 10.097 | 23.742 | 1.782
2019-06-21 04:30 | 135 | 1620 | 1.62 | 10.089 | 23.765 | 1.779
2019-06-21 04:45 | 136 | 1632 | 1.632 | 10.097 | 23.757 | 1.779
2019-06-21 05:00 | 135 | 1620 | 1.62 | 10.094 | 23.753 | 1.776
2019-06-21 05:15 | 136 | 1632 | 1.632 | 10.093 | 23.783 | 1.792
2019-06-21 05:30 | 136 | 1632 | 1.632 | 10.105 | 23.787 | 1.782
2019-06-21 05:45 | 135 | 1620 | 1.62 | 10.103 | 23.802 | 1.796
2019-06-21 06:00 | 135 | 1620 | 1.62 | 10.096 | 23.791 | 1.777
2019-06-21 06:15 | 134 | 1608 | 1.608 | 10.122 | 23.779 | 1.793
2019-06-21 06:30 | 135 | 1620 | 1.62 | 10.106 | 23.774 | 1.786
2019-06-21 06:45 | 135 | 1620 | 1.62 | 10.104 | 23.773 | 1.792
2019-06-21 07:00 | 135 | 1620 | 1.62 | 10.122 | 23.752 | 1.786
2019-06-21 07:15 | 135 | 1620 | 1.62 | 10.107 | 23.76 | 1.789
2019-06-21 07:30 | 135 | 1620 | 1.62 | 10.088 | 23.766 | 1.791
2019-06-21 07:45 | 135 | 1620 | 1.62 | 10.095 | 23.736 | 1.787
2019-06-21 08:00 | 135 | 1620 | 1.62 | 10.089 | 23.739 | 1.788
2019-06-21 08:15 | 135 | 1620 | 1.62 | 10.094 | 23.742 | 1.794
2019-06-21 08:30 | 135 | 1620 | 1.62 | 10.088 | 23.728 | 1.79
2019-06-21 08:45 | 135 | 1620 | 1.62 | 10.087 | 23.764 | 1.788
2019-06-21 09:00 | 136 | 1632 | 1.632 | 10.079 | 23.772 | 1.792 | 0.96 | 1.7 | 24.15
2019-06-21 09:15 | 135 | 1620 | 1.62 | 10.107 | 23.764 | 1.792

## BH4 Raw Data
BH 4 |  |  |  | Temp | level depth to water (m)
| Count | Ltr/hr | M3/hr
2019-06-12 | 219 | 2628 | 2.628 | 9.918 | 1.946
2019-06-12 09:17 | 217 | 2604 | 2.604 | 9.97 | 1.948
2019-06-12 09:32 | 216 | 2592 | 2.592 | 9.948 | 1.945
2019-06-12 09:47 | 220 | 2640 | 2.64 | 9.968 | 1.936
2019-06-12 10:02 | 219 | 2628 | 2.628 | 9.971 | 1.947
2019-06-12 10:17 | 219 | 2628 | 2.628 | 9.969 | 1.941
2019-06-12 10:32 | 219 | 2628 | 2.628 | 9.955 | 1.931
2019-06-12 10:47 | 218 | 2616 | 2.616 | 9.95 | 1.925
2019-06-12 11:02 | 219 | 2628 | 2.628 | 9.95 | 1.94
2019-06-12 11:17 | 219 | 2628 | 2.628 | 9.952 | 1.93
2019-06-12 11:32 | 219 | 2628 | 2.628 | 9.978 | 1.932
2019-06-12 11:47 | 219 | 2628 | 2.628 | 9.971 | 1.928
2019-06-12 12:02 | 219 | 2628 | 2.628 | 9.973 | 1.925
2019-06-12 12:17 | 219 | 2628 | 2.628 | 9.953 | 1.92
2019-06-12 12:32 | 218 | 2616 | 2.616 | 9.948 | 1.926
2019-06-12 12:47 | 219 | 2628 | 2.628 | 9.973 | 1.928
2019-06-12 13:02 | 219 | 2628 | 2.628 | 9.967 | 1.913
2019-06-12 13:17 | 219 | 2628 | 2.628 | 9.97 | 1.918
2019-06-12 13:32 | 220 | 2640 | 2.64 | 9.954 | 1.906
2019-06-12 13:47 | 219 | 2628 | 2.628 | 9.953 | 1.906
2019-06-12 14:02 | 219 | 2628 | 2.628 | 9.959 | 1.902
2019-06-12 14:17 | 219 | 2628 | 2.628 | 9.967 | 1.904
2019-06-12 14:32 | 219 | 2628 | 2.628 | 9.945 | 1.913
2019-06-12 14:47 | 219 | 2628 | 2.628 | 9.968 | 1.894
2019-06-12 15:02 | 219 | 2628 | 2.628 | 9.982 | 1.917
2019-06-12 15:17 | 218 | 2616 | 2.616 | 9.973 | 1.906
2019-06-12 15:32 | 219 | 2628 | 2.628 | 9.969 | 1.913
2019-06-12 15:47 | 219 | 2628 | 2.628 | 9.965 | 1.909
2019-06-12 16:02 | 219 | 2628 | 2.628 | 9.953 | 1.917
2019-06-12 16:17 | 219 | 2628 | 2.628 | 9.958 | 1.909
2019-06-12 16:32 | 219 | 2628 | 2.628 | 9.951 | 1.917
2019-06-12 16:47 | 219 | 2628 | 2.628 | 9.995 | 1.91
2019-06-12 17:02 | 218 | 2616 | 2.616 | 9.962 | 1.899
2019-06-12 17:17 | 219 | 2628 | 2.628 | 9.977 | 1.899
2019-06-12 17:32 | 219 | 2628 | 2.628 | 9.975 | 1.898
2019-06-12 17:47 | 219 | 2628 | 2.628 | 9.974 | 1.918
2019-06-12 18:02 | 219 | 2628 | 2.628 | 9.956 | 1.901
2019-06-12 18:17 | 219 | 2628 | 2.628 | 9.982 | 1.904
2019-06-12 18:32 | 219 | 2628 | 2.628 | 9.961 | 1.902
2019-06-12 18:47 | 219 | 2628 | 2.628 | 9.99 | 1.892
2019-06-12 19:02 | 219 | 2628 | 2.628 | 9.966 | 1.904
2019-06-12 19:17 | 219 | 2628 | 2.628 | 9.961 | 1.904
2019-06-12 19:32 | 219 | 2628 | 2.628 | 9.972 | 1.895
2019-06-12 19:47 | 219 | 2628 | 2.628 | 9.973 | 1.904
2019-06-12 20:02 | 219 | 2628 | 2.628 | 9.951 | 1.908
2019-06-12 20:17 | 219 | 2628 | 2.628 | 9.977 | 1.895
2019-06-12 20:32 | 219 | 2628 | 2.628 | 9.962 | 1.898
2019-06-12 20:47 | 219 | 2628 | 2.628 | 9.953 | 1.9
2019-06-12 21:02 | 220 | 2640 | 2.64 | 9.981 | 1.889
2019-06-12 21:17 | 218 | 2616 | 2.616 | 9.983 | 1.887
2019-06-12 21:32 | 219 | 2628 | 2.628 | 9.968 | 1.873
2019-06-12 21:47 | 219 | 2628 | 2.628 | 9.967 | 1.867
2019-06-12 22:02 | 219 | 2628 | 2.628 | 9.987 | 1.866
2019-06-12 22:17 | 218 | 2616 | 2.616 | 9.973 | 1.864
2019-06-12 22:32 | 219 | 2628 | 2.628 | 9.983 | 1.858
2019-06-12 22:47 | 220 | 2640 | 2.64 | 9.992 | 1.85
2019-06-12 23:02 | 219 | 2628 | 2.628 | 9.989 | 1.862
2019-06-12 23:17 | 218 | 2616 | 2.616 | 10.008 | 1.85
2019-06-12 23:32 | 219 | 2628 | 2.628 | 9.98 | 1.857
2019-06-12 23:47 | 219 | 2628 | 2.628 | 10.016 | 1.866
2019-06-13 00:02 | 219 | 2628 | 2.628 | 10.012 | 1.862
2019-06-13 00:17 | 218 | 2616 | 2.616 | 10.013 | 1.867
2019-06-13 00:32 | 219 | 2628 | 2.628 | 10.015 | 1.843
2019-06-13 00:47 | 219 | 2628 | 2.628 | 10.014 | 1.849
2019-06-13 01:02 | 219 | 2628 | 2.628 | 10.016 | 1.854
2019-06-13 01:17 | 219 | 2628 | 2.628 | 10.01 | 1.827
2019-06-13 01:32 | 219 | 2628 | 2.628 | 10.032 | 1.843
2019-06-13 01:47 | 218 | 2616 | 2.616 | 10.008 | 1.856
2019-06-13 02:02 | 220 | 2640 | 2.64 | 10.04 | 1.859
2019-06-13 02:17 | 218 | 2616 | 2.616 | 10.01 | 1.844
2019-06-13 02:32 | 219 | 2628 | 2.628 | 10.016 | 1.827
2019-06-13 02:47 | 218 | 2616 | 2.616 | 10.026 | 1.829
2019-06-13 03:02 | 219 | 2628 | 2.628 | 10.014 | 1.838
2019-06-13 03:17 | 219 | 2628 | 2.628 | 10.029 | 1.802
2019-06-13 03:32 | 219 | 2628 | 2.628 | 10.029 | 1.792
2019-06-13 03:47 | 219 | 2628 | 2.628 | 10.03 | 1.797
2019-06-13 04:02 | 219 | 2628 | 2.628 | 10.049 | 1.792
2019-06-13 04:17 | 218 | 2616 | 2.616 | 10.068 | 1.764
2019-06-13 04:32 | 219 | 2628 | 2.628 | 10.082 | 1.781
2019-06-13 04:47 | 219 | 2628 | 2.628 | 10.083 | 1.767
2019-06-13 05:02 | 218 | 2616 | 2.616 | 10.108 | 1.751
2019-06-13 05:17 | 219 | 2628 | 2.628 | 10.131 | 1.75
2019-06-13 05:32 | 218 | 2616 | 2.616 | 10.088 | 1.739
2019-06-13 05:47 | 218 | 2616 | 2.616 | 10.108 | 1.738
2019-06-13 06:02 | 219 | 2628 | 2.628 | 10.136 | 1.747
2019-06-13 06:17 | 219 | 2628 | 2.628 | 10.134 | 1.734
2019-06-13 06:32 | 218 | 2616 | 2.616 | 10.12 | 1.715
2019-06-13 06:47 | 218 | 2616 | 2.616 | 10.151 | 1.71
2019-06-13 07:02 | 218 | 2616 | 2.616 | 10.164 | 1.696
2019-06-13 07:17 | 219 | 2628 | 2.628 | 10.14 | 1.699
2019-06-13 07:32 | 218 | 2616 | 2.616 | 10.168 | 1.686
2019-06-13 07:47 | 218 | 2616 | 2.616 | 10.155 | 1.684
2019-06-13 08:02 | 218 | 2616 | 2.616 | 10.173 | 1.676
2019-06-13 08:17 | 219 | 2628 | 2.628 | 10.171 | 1.686
2019-06-13 08:32 | 218 | 2616 | 2.616 | 10.173 | 1.704
2019-06-13 08:47 | 250 | 3000 | 3 | 10.172 | 1.71
2019-06-13 09:02 | 251 | 3012 | 3.012 | 10.173 | 1.708
2019-06-13 09:17 | 250 | 3000 | 3 | 10.157 | 1.704
2019-06-13 09:32 | 250 | 3000 | 3 | 10.171 | 1.694
2019-06-13 09:47 | 250 | 3000 | 3 | 10.178 | 1.686
2019-06-13 10:02 | 250 | 3000 | 3 | 10.154 | 1.667
2019-06-13 10:17 | 250 | 3000 | 3 | 10.151 | 1.66
2019-06-13 10:32 | 250 | 3000 | 3 | 10.14 | 1.658
2019-06-13 10:47 | 250 | 3000 | 3 | 10.143 | 1.656
2019-06-13 11:02 | 250 | 3000 | 3 | 10.115 | 1.639
2019-06-13 11:17 | 250 | 3000 | 3 | 10.122 | 1.64
2019-06-13 11:32 | 251 | 3012 | 3.012 | 10.107 | 1.628
2019-06-13 11:47 | 250 | 3000 | 3 | 10.094 | 1.623
2019-06-13 12:02 | 251 | 3012 | 3.012 | 10.097 | 1.623
2019-06-13 12:17 | 250 | 3000 | 3 | 10.087 | 1.608
2019-06-13 12:32 | 250 | 3000 | 3 | 10.084 | 1.606
2019-06-13 12:47 | 251 | 3012 | 3.012 | 10.062 | 1.597
2019-06-13 13:02 | 250 | 3000 | 3 | 10.036 | 1.602
2019-06-13 13:17 | 250 | 3000 | 3 | 10.026 | 1.608
2019-06-13 13:32 | 250 | 3000 | 3 | 10.002 | 1.591
2019-06-13 13:47 | 250 | 3000 | 3 | 10.012 | 1.588
2019-06-13 14:02 | 250 | 3000 | 3 | 9.992 | 1.582
2019-06-13 14:17 | 250 | 3000 | 3 | 9.99 | 1.584
2019-06-13 14:32 | 250 | 3000 | 3 | 9.977 | 1.578
2019-06-13 14:47 | 250 | 3000 | 3 | 9.963 | 1.575
2019-06-13 15:02 | 250 | 3000 | 3 | 9.956 | 1.568
2019-06-13 15:17 | 250 | 3000 | 3 | 9.951 | 1.573
2019-06-13 15:32 | 250 | 3000 | 3 | 9.942 | 1.566
2019-06-13 15:47 | 250 | 3000 | 3 | 9.932 | 1.565
2019-06-13 16:02 | 250 | 3000 | 3 | 9.926 | 1.565
2019-06-13 16:17 | 251 | 3012 | 3.012 | 9.916 | 1.559
2019-06-13 16:32 | 250 | 3000 | 3 | 9.903 | 1.561
2019-06-13 16:47 | 250 | 3000 | 3 | 9.919 | 1.558
2019-06-13 17:02 | 249 | 2988 | 2.988 | 9.893 | 1.551
2019-06-13 17:17 | 251 | 3012 | 3.012 | 9.892 | 1.552
2019-06-13 17:32 | 250 | 3000 | 3 | 9.88 | 1.55
2019-06-13 17:47 | 251 | 3012 | 3.012 | 9.897 | 1.548
2019-06-13 18:02 | 250 | 3000 | 3 | 9.892 | 1.545
2019-06-13 18:17 | 250 | 3000 | 3 | 9.888 | 1.551
2019-06-13 18:32 | 251 | 3012 | 3.012 | 9.865 | 1.536
2019-06-13 18:47 | 250 | 3000 | 3 | 9.853 | 1.556
2019-06-13 19:02 | 251 | 3012 | 3.012 | 9.866 | 1.542
2019-06-13 19:17 | 250 | 3000 | 3 | 9.858 | 1.549
2019-06-13 19:32 | 250 | 3000 | 3 | 9.856 | 1.546
2019-06-13 19:47 | 250 | 3000 | 3 | 9.854 | 1.538
2019-06-13 20:02 | 250 | 3000 | 3 | 9.859 | 1.55
2019-06-13 20:17 | 250 | 3000 | 3 | 9.843 | 1.539
2019-06-13 20:32 | 250 | 3000 | 3 | 9.835 | 1.552
2019-06-13 20:47 | 250 | 3000 | 3 | 9.815 | 1.538
2019-06-13 21:02 | 250 | 3000 | 3 | 9.815 | 1.538
2019-06-13 21:17 | 250 | 3000 | 3 | 9.843 | 1.536
2019-06-13 21:32 | 250 | 3000 | 3 | 9.835 | 1.532
2019-06-13 21:47 | 250 | 3000 | 3 | 9.835 | 1.534
2019-06-13 22:02 | 250 | 3000 | 3 | 9.81 | 1.537
2019-06-13 22:17 | 250 | 3000 | 3 | 9.828 | 1.539
2019-06-13 22:32 | 250 | 3000 | 3 | 9.82 | 1.535
2019-06-13 22:47 | 250 | 3000 | 3 | 9.82 | 1.522
2019-06-13 23:02 | 250 | 3000 | 3 | 9.806 | 1.537
2019-06-13 23:17 | 250 | 3000 | 3 | 9.801 | 1.527
2019-06-13 23:32 | 250 | 3000 | 3 | 9.789 | 1.532
2019-06-13 23:47 | 251 | 3012 | 3.012 | 9.821 | 1.535
2019-06-14 00:02 | 250 | 3000 | 3 | 9.818 | 1.529
2019-06-14 00:17 | 250 | 3000 | 3 | 9.812 | 1.525
2019-06-14 00:32 | 250 | 3000 | 3 | 9.806 | 1.531
2019-06-14 00:47 | 250 | 3000 | 3 | 9.804 | 1.536
2019-06-14 01:02 | 250 | 3000 | 3 | 9.802 | 1.533
2019-06-14 01:17 | 251 | 3012 | 3.012 | 9.804 | 1.533
2019-06-14 01:32 | 250 | 3000 | 3 | 9.812 | 1.537
2019-06-14 01:47 | 250 | 3000 | 3 | 9.795 | 1.511
2019-06-14 02:02 | 250 | 3000 | 3 | 9.819 | 1.532
2019-06-14 02:17 | 250 | 3000 | 3 | 9.802 | 1.519
2019-06-14 02:32 | 251 | 3012 | 3.012 | 9.823 | 1.536
2019-06-14 02:47 | 251 | 3012 | 3.012 | 9.794 | 1.531
2019-06-14 03:02 | 250 | 3000 | 3 | 9.794 | 1.541
2019-06-14 03:17 | 250 | 3000 | 3 | 9.817 | 1.523
2019-06-14 03:32 | 251 | 3012 | 3.012 | 9.804 | 1.53
2019-06-14 03:47 | 250 | 3000 | 3 | 9.801 | 1.526
2019-06-14 04:02 | 250 | 3000 | 3 | 9.806 | 1.535
2019-06-14 04:17 | 250 | 3000 | 3 | 9.805 | 1.534
2019-06-14 04:32 | 250 | 3000 | 3 | 9.786 | 1.525
2019-06-14 04:47 | 250 | 3000 | 3 | 9.78 | 1.526
2019-06-14 05:02 | 251 | 3012 | 3.012 | 9.811 | 1.528
2019-06-14 05:17 | 249 | 2988 | 2.988 | 9.818 | 1.522
2019-06-14 05:32 | 250 | 3000 | 3 | 9.812 | 1.539
2019-06-14 05:47 | 249 | 2988 | 2.988 | 9.782 | 1.534
2019-06-14 06:02 | 250 | 3000 | 3 | 9.79 | 1.531
2019-06-14 06:17 | 250 | 3000 | 3 | 9.784 | 1.539
2019-06-14 06:32 | 250 | 3000 | 3 | 9.809 | 1.549
2019-06-14 06:47 | 250 | 3000 | 3 | 9.805 | 1.545
2019-06-14 07:02 | 251 | 3012 | 3.012 | 9.799 | 1.547
2019-06-14 07:17 | 250 | 3000 | 3 | 9.818 | 1.539
2019-06-14 07:32 | 249 | 2988 | 2.988 | 9.796 | 1.533
2019-06-14 07:47 | 250 | 3000 | 3 | 9.808 | 1.552
2019-06-14 08:02 | 249 | 2988 | 2.988 | 9.803 | 1.537
2019-06-14 08:17 | 250 | 3000 | 3 | 9.801 | 1.543
2019-06-14 08:32 | 250 | 3000 | 3 | 9.812 | 1.551
2019-06-14 08:47 | 250 | 3000 | 3 | 9.801 | 1.537
2019-06-14 09:02 | 250 | 3000 | 3 | 9.814 | 1.55
2019-06-14 09:17 | 250 | 3000 | 3 | 9.804 | 1.553
2019-06-14 09:32 | 250 | 3000 | 3 | 9.818 | 1.55
2019-06-14 09:47 | 250 | 3000 | 3 | 9.81 | 1.545
2019-06-14 10:02 | 248 | 2976 | 2.976 | 9.818 | 1.555
2019-06-14 10:17 | 246 | 2952 | 2.952 | 9.803 | 1.541
2019-06-14 10:32 | 249 | 2988 | 2.988 | 9.799 | 1.547
2019-06-14 10:47 | 249 | 2988 | 2.988 | 9.826 | 1.556
2019-06-14 11:02 | 249 | 2988 | 2.988 | 9.821 | 1.555
2019-06-14 11:17 | 249 | 2988 | 2.988 | 9.798 | 1.549
2019-06-14 11:32 | 249 | 2988 | 2.988 | 9.829 | 1.555
2019-06-14 11:47 | 249 | 2988 | 2.988 | 9.815 | 1.567
2019-06-14 12:02 | 249 | 2988 | 2.988 | 9.824 | 1.567
2019-06-14 12:17 | 249 | 2988 | 2.988 | 9.837 | 1.546
2019-06-14 12:32 | 248 | 2976 | 2.976 | 9.838 | 1.557
2019-06-14 12:47 | 249 | 2988 | 2.988 | 9.832 | 1.564
2019-06-14 13:02 | 248 | 2976 | 2.976 | 9.849 | 1.559
2019-06-14 13:17 | 249 | 2988 | 2.988 | 9.827 | 1.558
2019-06-14 13:32 | 248 | 2976 | 2.976 | 9.838 | 1.56
2019-06-14 13:47 | 248 | 2976 | 2.976 | 9.818 | 1.562
2019-06-14 14:02 | 249 | 2988 | 2.988 | 9.818 | 1.556
2019-06-14 14:17 | 248 | 2976 | 2.976 | 9.857 | 1.557
2019-06-14 14:32 | 248 | 2976 | 2.976 | 9.849 | 1.566
2019-06-14 14:47 | 248 | 2976 | 2.976 | 9.834 | 1.569
2019-06-14 15:02 | 249 | 2988 | 2.988 | 9.856 | 1.561
2019-06-14 15:17 | 248 | 2976 | 2.976 | 9.835 | 1.577
2019-06-14 15:32 | 248 | 2976 | 2.976 | 9.839 | 1.56
2019-06-14 15:47 | 248 | 2976 | 2.976 | 9.86 | 1.58
2019-06-14 16:02 | 248 | 2976 | 2.976 | 9.833 | 1.581
2019-06-14 16:17 | 248 | 2976 | 2.976 | 9.852 | 1.565
2019-06-14 16:32 | 248 | 2976 | 2.976 | 9.843 | 1.582
2019-06-14 16:47 | 248 | 2976 | 2.976 | 9.827 | 1.57
2019-06-14 17:02 | 247 | 2964 | 2.964 | 9.835 | 1.579
2019-06-14 17:17 | 248 | 2976 | 2.976 | 9.846 | 1.582
2019-06-14 17:32 | 248 | 2976 | 2.976 | 9.883 | 1.592
2019-06-14 17:47 | 248 | 2976 | 2.976 | 9.83 | 1.578
2019-06-14 18:02 | 248 | 2976 | 2.976 | 9.884 | 1.579
2019-06-14 18:17 | 247 | 2964 | 2.964 | 9.879 | 1.579
2019-06-14 18:32 | 248 | 2976 | 2.976 | 9.833 | 1.579
2019-06-14 18:47 | 248 | 2976 | 2.976 | 9.869 | 1.592
2019-06-14 19:02 | 247 | 2964 | 2.964 | 9.867 | 1.584
2019-06-14 19:17 | 248 | 2976 | 2.976 | 9.85 | 1.587
2019-06-14 19:32 | 247 | 2964 | 2.964 | 9.863 | 1.591
2019-06-14 19:47 | 247 | 2964 | 2.964 | 9.863 | 1.59
2019-06-14 20:02 | 248 | 2976 | 2.976 | 9.879 | 1.597
2019-06-14 20:17 | 248 | 2976 | 2.976 | 9.842 | 1.595
2019-06-14 20:32 | 248 | 2976 | 2.976 | 9.84 | 1.593
2019-06-14 20:47 | 247 | 2964 | 2.964 | 9.878 | 1.59
2019-06-14 21:02 | 248 | 2976 | 2.976 | 9.87 | 1.598
2019-06-14 21:17 | 248 | 2976 | 2.976 | 9.882 | 1.608
2019-06-14 21:32 | 248 | 2976 | 2.976 | 9.856 | 1.613
2019-06-14 21:47 | 248 | 2976 | 2.976 | 9.845 | 1.608
2019-06-14 22:02 | 248 | 2976 | 2.976 | 9.869 | 1.609
2019-06-14 22:17 | 248 | 2976 | 2.976 | 9.864 | 1.61
2019-06-14 22:32 | 248 | 2976 | 2.976 | 9.883 | 1.614
2019-06-14 22:47 | 248 | 2976 | 2.976 | 9.864 | 1.619
2019-06-14 23:02 | 248 | 2976 | 2.976 | 9.877 | 1.616
2019-06-14 23:17 | 248 | 2976 | 2.976 | 9.889 | 1.606
2019-06-14 23:32 | 247 | 2964 | 2.964 | 9.89 | 1.616
2019-06-14 23:47 | 248 | 2976 | 2.976 | 9.869 | 1.607
2019-06-15 00:02 | 249 | 2988 | 2.988 | 9.875 | 1.618
2019-06-15 00:17 | 248 | 2976 | 2.976 | 9.882 | 1.617
2019-06-15 00:32 | 248 | 2976 | 2.976 | 9.892 | 1.618
2019-06-15 00:47 | 248 | 2976 | 2.976 | 9.86 | 1.624
2019-06-15 01:02 | 248 | 2976 | 2.976 | 9.891 | 1.625
2019-06-15 01:17 | 247 | 2964 | 2.964 | 9.877 | 1.624
2019-06-15 01:32 | 248 | 2976 | 2.976 | 9.88 | 1.632
2019-06-15 01:47 | 247 | 2964 | 2.964 | 9.908 | 1.618
2019-06-15 02:02 | 248 | 2976 | 2.976 | 9.885 | 1.639
2019-06-15 02:17 | 248 | 2976 | 2.976 | 9.892 | 1.637
2019-06-15 02:32 | 248 | 2976 | 2.976 | 9.894 | 1.644
2019-06-15 02:47 | 247 | 2964 | 2.964 | 9.9 | 1.621
2019-06-15 03:02 | 248 | 2976 | 2.976 | 9.912 | 1.62
2019-06-15 03:17 | 247 | 2964 | 2.964 | 9.904 | 1.626
2019-06-15 03:32 | 248 | 2976 | 2.976 | 9.891 | 1.636
2019-06-15 03:47 | 248 | 2976 | 2.976 | 9.879 | 1.633
2019-06-15 04:02 | 248 | 2976 | 2.976 | 9.894 | 1.631
2019-06-15 04:17 | 247 | 2964 | 2.964 | 9.92 | 1.638
2019-06-15 04:32 | 248 | 2976 | 2.976 | 9.892 | 1.641
2019-06-15 04:47 | 247 | 2964 | 2.964 | 9.919 | 1.632
2019-06-15 05:02 | 248 | 2976 | 2.976 | 9.914 | 1.63
2019-06-15 05:17 | 247 | 2964 | 2.964 | 9.897 | 1.639
2019-06-15 05:32 | 247 | 2964 | 2.964 | 9.907 | 1.642
2019-06-15 05:47 | 247 | 2964 | 2.964 | 9.905 | 1.643
2019-06-15 06:02 | 248 | 2976 | 2.976 | 9.912 | 1.657
2019-06-15 06:17 | 248 | 2976 | 2.976 | 9.914 | 1.637
2019-06-15 06:32 | 248 | 2976 | 2.976 | 9.899 | 1.646
2019-06-15 06:47 | 248 | 2976 | 2.976 | 9.904 | 1.64
2019-06-15 07:02 | 247 | 2964 | 2.964 | 9.91 | 1.646
2019-06-15 07:17 | 248 | 2976 | 2.976 | 9.884 | 1.658
2019-06-15 07:32 | 248 | 2976 | 2.976 | 9.91 | 1.649
2019-06-15 07:47 | 248 | 2976 | 2.976 | 9.908 | 1.655
2019-06-15 08:02 | 248 | 2976 | 2.976 | 9.929 | 1.648
2019-06-15 08:17 | 247 | 2964 | 2.964 | 9.899 | 1.646
2019-06-15 08:32 | 247 | 2964 | 2.964 | 9.917 | 1.647
2019-06-15 08:47 | 247 | 2964 | 2.964 | 9.936 | 1.661
2019-06-15 09:02 | 247 | 2964 | 2.964 | 9.913 | 1.658
2019-06-15 09:17 | 248 | 2976 | 2.976 | 9.9 | 1.662
2019-06-15 09:32 | 247 | 2964 | 2.964 | 9.914 | 1.671
2019-06-15 09:47 | 244 | 2928 | 2.928 | 9.917 | 1.66
2019-06-15 10:02 | 247 | 2964 | 2.964 | 9.908 | 1.681
2019-06-15 10:17 | 247 | 2964 | 2.964 | 9.898 | 1.492
2019-06-15 10:32 | 177 | 2124 | 2.124 | 9.93 | 1.427
2019-06-15 10:47 | 0 | 0 | 0 | 10.312 | 1.427
2019-06-15 11:02 | 0 | 0 | 0 | 10.362 | 1.405
2019-06-15 11:17 | 0 | 0 | 0 | 10.232 | 1.406
2019-06-15 11:32 | 0 | 0 | 0 | 10.122 | 1.424
2019-06-15 11:47 | 0 | 0 | 0 | 10.102 | 1.413
2019-06-15 12:02 | 0 | 0 | 0 | 10.076 | 1.4
2019-06-15 12:17 | 0 | 0 | 0 | 10.038 | 1.411
2019-06-15 12:32 | 0 | 0 | 0 | 10.044 | 1.409
2019-06-15 12:47 | 0 | 0 | 0 | 10.007 | 1.4
2019-06-15 13:02 | 0 | 0 | 0 | 10.03 | 1.408
2019-06-15 13:17 | 0 | 0 | 0 | 10.01 | 1.413
2019-06-15 13:32 | 0 | 0 | 0 | 10.011 | 1.411
2019-06-15 13:47 | 0 | 0 | 0 | 9.991 | 1.413
2019-06-15 14:02 | 0 | 0 | 0 | 9.979 | 1.42
2019-06-15 14:17 | 0 | 0 | 0 | 10.001 | 1.409
2019-06-15 14:32 | 0 | 0 | 0 | 9.981 | 1.414
2019-06-15 14:47 | 0 | 0 | 0 | 9.982 | 1.409
2019-06-15 15:02 | 0 | 0 | 0 | 9.94 | 1.414
2019-06-15 15:17 | 0 | 0 | 0 | 9.968 | 1.413
2019-06-15 15:32 | 0 | 0 | 0 | 9.945 | 1.421
2019-06-15 15:47 | 0 | 0 | 0 | 9.964 | 1.413
2019-06-15 16:02 | 0 | 0 | 0 | 9.955 | 1.413
2019-06-15 16:17 | 0 | 0 | 0 | 9.967 | 1.413
2019-06-15 16:32 | 0 | 0 | 0 | 9.959 | 1.412
2019-06-15 16:47 | 0 | 0 | 0 | 9.951 | 1.416
2019-06-15 17:02 | 0 | 0 | 0 | 9.963 | 1.408
2019-06-15 17:17 | 0 | 0 | 0 | 9.952 | 1.416
2019-06-15 17:32 | 0 | 0 | 0 | 9.96 | 1.414
2019-06-15 17:47 | 0 | 0 | 0 | 9.956 | 1.426
2019-06-15 18:02 | 0 | 0 | 0 | 9.961 | 1.419
2019-06-15 18:17 | 0 | 0 | 0 | 9.948 | 1.416
2019-06-15 18:32 | 0 | 0 | 0 | 9.922 | 1.419
2019-06-15 18:47 | 0 | 0 | 0 | 9.945 | 1.414
2019-06-15 19:02 | 0 | 0 | 0 | 9.962 | 1.428
2019-06-15 19:17 | 0 | 0 | 0 | 9.946 | 1.422
2019-06-15 19:32 | 0 | 0 | 0 | 9.941 | 1.412
2019-06-15 19:47 | 0 | 0 | 0 | 9.941 | 1.418
2019-06-15 20:02 | 0 | 0 | 0 | 9.95 | 1.424
2019-06-15 20:17 | 0 | 0 | 0 | 9.931 | 1.429
2019-06-15 20:32 | 0 | 0 | 0 | 9.934 | 1.422
2019-06-15 20:47 | 0 | 0 | 0 | 9.95 | 1.421
2019-06-15 21:02 | 0 | 0 | 0 | 9.939 | 1.43
2019-06-15 21:17 | 0 | 0 | 0 | 9.962 | 1.422
2019-06-15 21:32 | 0 | 0 | 0 | 9.922 | 1.421
2019-06-15 21:47 | 0 | 0 | 0 | 9.939 | 1.418
2019-06-15 22:02 | 0 | 0 | 0 | 9.929 | 1.431
2019-06-15 22:17 | 0 | 0 | 0 | 9.929 | 1.423
2019-06-15 22:32 | 0 | 0 | 0 | 9.964 | 1.427
2019-06-15 22:47 | 0 | 0 | 0 | 9.914 | 1.426
2019-06-15 23:02 | 0 | 0 | 0 | 9.919 | 1.43
2019-06-15 23:17 | 0 | 0 | 0 | 9.932 | 1.427
2019-06-15 23:32 | 0 | 0 | 0 | 9.938 | 1.434
2019-06-15 23:47 | 0 | 0 | 0 | 9.939 | 1.422
2019-06-16 00:02 | 0 | 0 | 0 | 9.92 | 1.422
2019-06-16 00:17 | 0 | 0 | 0 | 9.94 | 1.433
2019-06-16 00:32 | 0 | 0 | 0 | 9.957 | 1.43
2019-06-16 00:47 | 0 | 0 | 0 | 9.939 | 1.429
2019-06-16 01:02 | 0 | 0 | 0 | 9.928 | 1.42
2019-06-16 01:17 | 0 | 0 | 0 | 9.936 | 1.418
2019-06-16 01:32 | 0 | 0 | 0 | 9.934 | 1.438
2019-06-16 01:47 | 0 | 0 | 0 | 9.925 | 1.437
2019-06-16 02:02 | 0 | 0 | 0 | 9.938 | 1.435
2019-06-16 02:17 | 0 | 0 | 0 | 9.946 | 1.434
2019-06-16 02:32 | 0 | 0 | 0 | 9.917 | 1.439
2019-06-16 02:47 | 0 | 0 | 0 | 9.925 | 1.442
2019-06-16 03:02 | 0 | 0 | 0 | 9.955 | 1.428
2019-06-16 03:17 | 0 | 0 | 0 | 9.94 | 1.431
2019-06-16 03:32 | 0 | 0 | 0 | 9.94 | 1.421
2019-06-16 03:47 | 0 | 0 | 0 | 9.925 | 1.431
2019-06-16 04:02 | 0 | 0 | 0 | 9.909 | 1.431
2019-06-16 04:17 | 0 | 0 | 0 | 9.931 | 1.443
2019-06-16 04:32 | 0 | 0 | 0 | 9.931 | 1.43
2019-06-16 04:47 | 0 | 0 | 0 | 9.944 | 1.431
2019-06-16 05:02 | 0 | 0 | 0 | 9.934 | 1.429
2019-06-16 05:17 | 0 | 0 | 0 | 9.921 | 1.436
2019-06-16 05:32 | 0 | 0 | 0 | 9.922 | 1.436
2019-06-16 05:47 | 0 | 0 | 0 | 9.909 | 1.428
2019-06-16 06:02 | 0 | 0 | 0 | 9.93 | 1.448
2019-06-16 06:17 | 0 | 0 | 0 | 9.941 | 1.432
2019-06-16 06:32 | 0 | 0 | 0 | 9.93 | 1.443
2019-06-16 06:47 | 0 | 0 | 0 | 9.948 | 1.45
2019-06-16 07:02 | 0 | 0 | 0 | 9.94 | 1.443
2019-06-16 07:17 | 0 | 0 | 0 | 9.953 | 1.44
2019-06-16 07:32 | 0 | 0 | 0 | 9.93 | 1.441
2019-06-16 07:47 | 0 | 0 | 0 | 9.924 | 1.444
2019-06-16 08:02 | 0 | 0 | 0 | 9.917 | 1.436
2019-06-16 08:17 | 0 | 0 | 0 | 9.939 | 1.445
2019-06-16 08:32 | 0 | 0 | 0 | 9.93 | 1.444
2019-06-16 08:47 | 0 | 0 | 0 | 9.942 | 1.434
2019-06-16 09:02 | 0 | 0 | 0 | 9.953 | 1.444
2019-06-16 09:17 | 0 | 0 | 0 | 9.921 | 1.445
2019-06-16 09:32 | 0 | 0 | 0 | 9.922 | 1.442
2019-06-16 09:47 | 0 | 0 | 0 | 9.935 | 1.446
2019-06-16 10:02 | 0 | 0 | 0 | 9.954 | 1.449
2019-06-16 10:17 | 0 | 0 | 0 | 9.931 | 1.448
2019-06-16 10:32 | 0 | 0 | 0 | 9.931 | 1.449
2019-06-16 10:47 | 0 | 0 | 0 | 9.925 | 1.455
2019-06-16 11:02 | 0 | 0 | 0 | 9.92 | 1.44
2019-06-16 11:17 | 0 | 0 | 0 | 9.908 | 1.455
2019-06-16 11:32 | 0 | 0 | 0 | 9.939 | 1.45
2019-06-16 11:47 | 0 | 0 | 0 | 9.931 | 1.451
2019-06-16 12:02 | 0 | 0 | 0 | 9.925 | 1.448
2019-06-16 12:17 | 0 | 0 | 0 | 9.942 | 1.45
2019-06-16 12:32 | 0 | 0 | 0 | 9.956 | 1.452
2019-06-16 12:47 | 0 | 0 | 0 | 9.916 | 1.453
2019-06-16 13:02 | 0 | 0 | 0 | 9.919 | 1.461
2019-06-16 13:17 | 0 | 0 | 0 | 9.953 | 1.451
2019-06-16 13:32 | 0 | 0 | 0 | 9.942 | 1.452
2019-06-16 13:47 | 0 | 0 | 0 | 9.953 | 1.464
2019-06-16 14:02 | 0 | 0 | 0 | 9.92 | 1.453
2019-06-16 14:17 | 0 | 0 | 0 | 9.947 | 1.466
2019-06-16 14:32 | 0 | 0 | 0 | 9.942 | 1.461
2019-06-16 14:47 | 0 | 0 | 0 | 9.925 | 1.455
2019-06-16 15:02 | 0 | 0 | 0 | 9.925 | 1.45
2019-06-16 15:17 | 0 | 0 | 0 | 9.929 | 1.462
2019-06-16 15:32 | 0 | 0 | 0 | 9.931 | 1.466
2019-06-16 15:47 | 0 | 0 | 0 | 9.925 | 1.458
2019-06-16 16:02 | 0 | 0 | 0 | 9.928 | 1.457
2019-06-16 16:17 | 0 | 0 | 0 | 9.926 | 1.455
2019-06-16 16:32 | 0 | 0 | 0 | 9.935 | 1.455
2019-06-16 16:47 | 0 | 0 | 0 | 9.928 | 1.458
2019-06-16 17:02 | 0 | 0 | 0 | 9.939 | 1.454
2019-06-16 17:17 | 0 | 0 | 0 | 9.943 | 1.456
2019-06-16 17:32 | 0 | 0 | 0 | 9.934 | 1.473
2019-06-16 17:47 | 0 | 0 | 0 | 9.911 | 1.458
2019-06-16 18:02 | 0 | 0 | 0 | 9.94 | 1.464
2019-06-16 18:17 | 0 | 0 | 0 | 9.928 | 1.451
2019-06-16 18:32 | 0 | 0 | 0 | 9.956 | 1.465
2019-06-16 18:47 | 0 | 0 | 0 | 9.958 | 1.461
2019-06-16 19:02 | 0 | 0 | 0 | 9.921 | 1.46
2019-06-16 19:17 | 0 | 0 | 0 | 9.924 | 1.478
2019-06-16 19:32 | 0 | 0 | 0 | 9.938 | 1.461
2019-06-16 19:47 | 0 | 0 | 0 | 9.913 | 1.462
2019-06-16 20:02 | 0 | 0 | 0 | 9.931 | 1.45
2019-06-16 20:17 | 0 | 0 | 0 | 9.924 | 1.46
2019-06-16 20:32 | 0 | 0 | 0 | 9.929 | 1.465
2019-06-16 20:47 | 0 | 0 | 0 | 9.927 | 1.475
2019-06-16 21:02 | 0 | 0 | 0 | 9.959 | 1.46
2019-06-16 21:17 | 0 | 0 | 0 | 9.961 | 1.462
2019-06-16 21:32 | 0 | 0 | 0 | 9.938 | 1.458
2019-06-16 21:47 | 0 | 0 | 0 | 9.939 | 1.462
2019-06-16 22:02 | 0 | 0 | 0 | 9.944 | 1.466
2019-06-16 22:17 | 0 | 0 | 0 | 9.958 | 1.462
2019-06-16 22:32 | 0 | 0 | 0 | 9.931 | 1.469
2019-06-16 22:47 | 0 | 0 | 0 | 9.942 | 1.467
2019-06-16 23:02 | 0 | 0 | 0 | 9.927 | 1.459
2019-06-16 23:17 | 0 | 0 | 0 | 9.948 | 1.461
2019-06-16 23:32 | 0 | 0 | 0 | 9.939 | 1.458
2019-06-16 23:47 | 0 | 0 | 0 | 9.951 | 1.46
2019-06-17 00:02 | 0 | 0 | 0 | 9.934 | 1.467
2019-06-17 00:17 | 0 | 0 | 0 | 9.929 | 1.465
2019-06-17 00:32 | 0 | 0 | 0 | 9.936 | 1.469
2019-06-17 00:47 | 0 | 0 | 0 | 9.955 | 1.465
2019-06-17 01:02 | 0 | 0 | 0 | 9.932 | 1.463
2019-06-17 01:17 | 0 | 0 | 0 | 9.934 | 1.455
2019-06-17 01:32 | 0 | 0 | 0 | 9.933 | 1.457
2019-06-17 01:47 | 0 | 0 | 0 | 9.931 | 1.454
2019-06-17 02:02 | 0 | 0 | 0 | 9.936 | 1.457
2019-06-17 02:17 | 0 | 0 | 0 | 9.937 | 1.463
2019-06-17 02:32 | 0 | 0 | 0 | 9.95 | 1.451
2019-06-17 02:47 | 0 | 0 | 0 | 9.936 | 1.449
2019-06-17 03:02 | 0 | 0 | 0 | 9.932 | 1.45
2019-06-17 03:17 | 0 | 0 | 0 | 9.905 | 1.448
2019-06-17 03:32 | 0 | 0 | 0 | 9.911 | 1.467
2019-06-17 03:47 | 0 | 0 | 0 | 9.925 | 1.463
2019-06-17 04:02 | 0 | 0 | 0 | 9.952 | 1.464
2019-06-17 04:17 | 0 | 0 | 0 | 9.933 | 1.465
2019-06-17 04:32 | 0 | 0 | 0 | 9.942 | 1.459
2019-06-17 04:47 | 0 | 0 | 0 | 9.911 | 1.461
2019-06-17 05:02 | 0 | 0 | 0 | 9.933 | 1.46
2019-06-17 05:17 | 0 | 0 | 0 | 9.934 | 1.466
2019-06-17 05:32 | 0 | 0 | 0 | 9.951 | 1.458
2019-06-17 05:47 | 0 | 0 | 0 | 9.954 | 1.457
2019-06-17 06:02 | 0 | 0 | 0 | 9.94 | 1.464
2019-06-17 06:17 | 0 | 0 | 0 | 9.948 | 1.473
2019-06-17 06:32 | 0 | 0 | 0 | 9.959 | 1.462
2019-06-17 06:47 | 0 | 0 | 0 | 9.936 | 1.47
2019-06-17 07:02 | 0 | 0 | 0 | 9.936 | 1.462
2019-06-17 07:17 | 0 | 0 | 0 | 9.936 | 1.475
2019-06-17 07:32 | 0 | 0 | 0 | 9.928 | 1.462
2019-06-17 07:47 | 0 | 0 | 0 | 9.985 | 1.46
2019-06-17 08:02 | 0 | 0 | 0 | 9.956 | 1.655
2019-06-17 08:17 | 177 | 2124 | 2.124 | 9.893 | 1.68
2019-06-17 08:32 | 210 | 2520 | 2.52 | 9.733 | 1.712
2019-06-17 08:47 | 223 | 2676 | 2.676 | 9.693 | 1.708
2019-06-17 09:02 | 223 | 2676 | 2.676 | 9.738 | 1.72
2019-06-17 09:17 | 223 | 2676 | 2.676 | 9.795 | 1.718
2019-06-17 09:32 | 223 | 2676 | 2.676 | 9.824 | 1.723
2019-06-17 09:47 | 223 | 2676 | 2.676 | 9.861 | 1.711
2019-06-17 10:02 | 223 | 2676 | 2.676 | 9.9 | 1.73
2019-06-17 10:17 | 223 | 2676 | 2.676 | 9.912 | 1.709
2019-06-17 10:32 | 223 | 2676 | 2.676 | 9.924 | 1.727
2019-06-17 10:47 | 223 | 2676 | 2.676 | 9.916 | 1.73
2019-06-17 11:02 | 223 | 2676 | 2.676 | 9.931 | 1.718
2019-06-17 11:17 | 222 | 2664 | 2.664 | 9.925 | 1.729
2019-06-17 11:32 | 223 | 2676 | 2.676 | 9.925 | 1.736
2019-06-17 11:47 | 223 | 2676 | 2.676 | 9.948 | 1.723
2019-06-17 12:02 | 222 | 2664 | 2.664 | 9.936 | 1.735
2019-06-17 12:17 | 222 | 2664 | 2.664 | 9.969 | 1.727
2019-06-17 12:32 | 223 | 2676 | 2.676 | 9.965 | 1.735
2019-06-17 12:47 | 222 | 2664 | 2.664 | 9.976 | 1.728
2019-06-17 13:02 | 222 | 2664 | 2.664 | 9.965 | 1.731
2019-06-17 13:17 | 222 | 2664 | 2.664 | 9.941 | 1.743
2019-06-17 13:32 | 221 | 2652 | 2.652 | 9.968 | 1.727
2019-06-17 13:47 | 222 | 2664 | 2.664 | 9.97 | 1.719
2019-06-17 14:02 | 222 | 2664 | 2.664 | 9.975 | 1.721
2019-06-17 14:17 | 221 | 2652 | 2.652 | 9.982 | 1.735
2019-06-17 14:32 | 221 | 2652 | 2.652 | 9.979 | 1.742
2019-06-17 14:47 | 222 | 2664 | 2.664 | 9.982 | 1.739
2019-06-17 15:02 | 221 | 2652 | 2.652 | 9.981 | 1.738
2019-06-17 15:17 | 221 | 2652 | 2.652 | 9.981 | 1.734
2019-06-17 15:32 | 221 | 2652 | 2.652 | 9.968 | 1.725
2019-06-17 15:47 | 221 | 2652 | 2.652 | 9.97 | 1.738
2019-06-17 16:02 | 221 | 2652 | 2.652 | 9.973 | 1.742
2019-06-17 16:17 | 222 | 2664 | 2.664 | 9.956 | 1.737
2019-06-17 16:32 | 221 | 2652 | 2.652 | 9.965 | 1.752
2019-06-17 16:47 | 221 | 2652 | 2.652 | 9.998 | 1.744
2019-06-17 17:02 | 221 | 2652 | 2.652 | 9.965 | 1.742
2019-06-17 17:17 | 222 | 2664 | 2.664 | 9.987 | 1.742
2019-06-17 17:32 | 221 | 2652 | 2.652 | 9.969 | 1.737
2019-06-17 17:47 | 222 | 2664 | 2.664 | 9.986 | 1.731
2019-06-17 18:02 | 222 | 2664 | 2.664 | 9.98 | 1.743
2019-06-17 18:17 | 221 | 2652 | 2.652 | 9.995 | 1.749
2019-06-17 18:32 | 222 | 2664 | 2.664 | 10.001 | 1.755
2019-06-17 18:47 | 221 | 2652 | 2.652 | 10.01 | 1.741
2019-06-17 19:02 | 222 | 2664 | 2.664 | 9.978 | 1.747
2019-06-17 19:17 | 221 | 2652 | 2.652 | 9.979 | 1.737
2019-06-17 19:32 | 222 | 2664 | 2.664 | 9.967 | 1.756
2019-06-17 19:47 | 221 | 2652 | 2.652 | 9.983 | 1.755
2019-06-17 20:02 | 221 | 2652 | 2.652 | 9.995 | 1.752
2019-06-17 20:17 | 221 | 2652 | 2.652 | 9.967 | 1.763
2019-06-17 20:32 | 221 | 2652 | 2.652 | 9.993 | 1.743
2019-06-17 20:47 | 221 | 2652 | 2.652 | 9.982 | 1.755
2019-06-17 21:02 | 222 | 2664 | 2.664 | 9.975 | 1.746
2019-06-17 21:17 | 221 | 2652 | 2.652 | 9.996 | 1.754
2019-06-17 21:32 | 221 | 2652 | 2.652 | 9.97 | 1.745
2019-06-17 21:47 | 221 | 2652 | 2.652 | 9.981 | 1.743
2019-06-17 22:02 | 221 | 2652 | 2.652 | 9.971 | 1.752
2019-06-17 22:17 | 221 | 2652 | 2.652 | 9.962 | 1.746
2019-06-17 22:32 | 221 | 2652 | 2.652 | 9.998 | 1.751
2019-06-17 22:47 | 221 | 2652 | 2.652 | 9.979 | 1.747
2019-06-17 23:02 | 222 | 2664 | 2.664 | 9.998 | 1.761
2019-06-17 23:17 | 221 | 2652 | 2.652 | 9.979 | 1.763
2019-06-17 23:32 | 221 | 2652 | 2.652 | 9.986 | 1.757
2019-06-17 23:47 | 221 | 2652 | 2.652 | 9.99 | 1.749
2019-06-18 00:02 | 221 | 2652 | 2.652 | 9.979 | 1.764
2019-06-18 00:17 | 221 | 2652 | 2.652 | 9.98 | 1.754
2019-06-18 00:32 | 221 | 2652 | 2.652 | 9.996 | 1.749
2019-06-18 00:47 | 221 | 2652 | 2.652 | 9.979 | 1.763
2019-06-18 01:02 | 221 | 2652 | 2.652 | 9.964 | 1.762
2019-06-18 01:17 | 221 | 2652 | 2.652 | 10 | 1.765
2019-06-18 01:32 | 221 | 2652 | 2.652 | 10.004 | 1.756
2019-06-18 01:47 | 221 | 2652 | 2.652 | 9.987 | 1.767
2019-06-18 02:02 | 222 | 2664 | 2.664 | 9.994 | 1.765
2019-06-18 02:17 | 221 | 2652 | 2.652 | 9.976 | 1.763
2019-06-18 02:32 | 220 | 2640 | 2.64 | 10.007 | 1.758
2019-06-18 02:47 | 221 | 2652 | 2.652 | 9.971 | 1.754
2019-06-18 03:02 | 221 | 2652 | 2.652 | 9.977 | 1.756
2019-06-18 03:17 | 220 | 2640 | 2.64 | 10.004 | 1.763
2019-06-18 03:32 | 221 | 2652 | 2.652 | 9.99 | 1.759
2019-06-18 03:47 | 222 | 2664 | 2.664 | 9.981 | 1.771
2019-06-18 04:02 | 221 | 2652 | 2.652 | 9.978 | 1.768
2019-06-18 04:17 | 221 | 2652 | 2.652 | 9.995 | 1.756
2019-06-18 04:32 | 221 | 2652 | 2.652 | 9.99 | 1.768
2019-06-18 04:47 | 221 | 2652 | 2.652 | 9.999 | 1.772
2019-06-18 05:02 | 221 | 2652 | 2.652 | 9.979 | 1.759
2019-06-18 05:17 | 221 | 2652 | 2.652 | 9.986 | 1.76
2019-06-18 05:32 | 221 | 2652 | 2.652 | 10.004 | 1.757
2019-06-18 05:47 | 221 | 2652 | 2.652 | 9.963 | 1.756
2019-06-18 06:02 | 222 | 2664 | 2.664 | 9.982 | 1.756
2019-06-18 06:17 | 221 | 2652 | 2.652 | 9.967 | 1.764
2019-06-18 06:32 | 221 | 2652 | 2.652 | 9.965 | 1.769
2019-06-18 06:47 | 221 | 2652 | 2.652 | 9.997 | 1.759
2019-06-18 07:02 | 220 | 2640 | 2.64 | 9.959 | 1.766
2019-06-18 07:17 | 221 | 2652 | 2.652 | 9.99 | 1.765
2019-06-18 07:32 | 219 | 2628 | 2.628 | 9.978 | 1.755
2019-06-18 07:47 | 221 | 2652 | 2.652 | 9.973 | 1.763
2019-06-18 08:02 | 222 | 2664 | 2.664 | 9.967 | 1.767
2019-06-18 08:17 | 221 | 2652 | 2.652 | 9.976 | 1.768
2019-06-18 08:32 | 222 | 2664 | 2.664 | 9.984 | 1.769
2019-06-18 08:47 | 222 | 2664 | 2.664 | 9.989 | 1.769
2019-06-18 09:02 | 222 | 2664 | 2.664 | 9.982 | 1.774
2019-06-18 09:17 | 222 | 2664 | 2.664 | 9.967 | 1.761
2019-06-18 09:32 | 221 | 2652 | 2.652 | 9.976 | 1.762
2019-06-18 09:47 | 221 | 2652 | 2.652 | 9.971 | 1.78
2019-06-18 10:02 | 222 | 2664 | 2.664 | 9.969 | 1.765
2019-06-18 10:17 | 221 | 2652 | 2.652 | 9.975 | 1.78
2019-06-18 10:32 | 222 | 2664 | 2.664 | 9.964 | 1.764
2019-06-18 10:47 | 221 | 2652 | 2.652 | 9.976 | 1.787
2019-06-18 11:02 | 222 | 2664 | 2.664 | 9.967 | 1.769
2019-06-18 11:17 | 221 | 2652 | 2.652 | 9.972 | 1.758
2019-06-18 11:32 | 222 | 2664 | 2.664 | 9.971 | 1.776
2019-06-18 11:47 | 221 | 2652 | 2.652 | 9.977 | 1.768
2019-06-18 12:02 | 222 | 2664 | 2.664 | 9.98 | 1.767
2019-06-18 12:17 | 221 | 2652 | 2.652 | 9.991 | 1.771
2019-06-18 12:32 | 221 | 2652 | 2.652 | 9.963 | 1.772
2019-06-18 12:47 | 222 | 2664 | 2.664 | 9.979 | 1.774
2019-06-18 13:02 | 221 | 2652 | 2.652 | 9.992 | 1.779
2019-06-18 13:17 | 222 | 2664 | 2.664 | 9.98 | 1.782
2019-06-18 13:32 | 222 | 2664 | 2.664 | 9.976 | 1.789
2019-06-18 13:47 | 222 | 2664 | 2.664 | 9.956 | 1.785
2019-06-18 14:02 | 221 | 2652 | 2.652 | 9.961 | 1.778
2019-06-18 14:17 | 222 | 2664 | 2.664 | 9.986 | 1.79
2019-06-18 14:32 | 221 | 2652 | 2.652 | 9.967 | 1.782
2019-06-18 14:47 | 221 | 2652 | 2.652 | 9.996 | 1.787
2019-06-18 15:02 | 222 | 2664 | 2.664 | 9.979 | 1.772
2019-06-18 15:17 | 222 | 2664 | 2.664 | 9.982 | 1.786
2019-06-18 15:32 | 221 | 2652 | 2.652 | 9.973 | 1.772
2019-06-18 15:47 | 221 | 2652 | 2.652 | 9.994 | 1.771
2019-06-18 16:02 | 222 | 2664 | 2.664 | 9.979 | 1.772
2019-06-18 16:17 | 222 | 2664 | 2.664 | 9.975 | 1.776
2019-06-18 16:32 | 221 | 2652 | 2.652 | 9.996 | 1.776
2019-06-18 16:47 | 221 | 2652 | 2.652 | 9.953 | 1.778
2019-06-18 17:02 | 222 | 2664 | 2.664 | 9.99 | 1.785
2019-06-18 17:17 | 221 | 2652 | 2.652 | 9.985 | 1.793
2019-06-18 17:32 | 222 | 2664 | 2.664 | 9.959 | 1.785
2019-06-18 17:47 | 222 | 2664 | 2.664 | 9.988 | 1.779
2019-06-18 18:02 | 222 | 2664 | 2.664 | 9.973 | 1.78
2019-06-18 18:17 | 222 | 2664 | 2.664 | 9.996 | 1.777
2019-06-18 18:32 | 221 | 2652 | 2.652 | 9.976 | 1.789
2019-06-18 18:47 | 222 | 2664 | 2.664 | 9.976 | 1.785
2019-06-18 19:02 | 222 | 2664 | 2.664 | 9.998 | 1.795
2019-06-18 19:17 | 221 | 2652 | 2.652 | 9.989 | 1.781
2019-06-18 19:32 | 222 | 2664 | 2.664 | 9.964 | 1.781
2019-06-18 19:47 | 222 | 2664 | 2.664 | 9.962 | 1.793
2019-06-18 20:02 | 222 | 2664 | 2.664 | 9.971 | 1.772
2019-06-18 20:17 | 221 | 2652 | 2.652 | 9.97 | 1.785
2019-06-18 20:32 | 222 | 2664 | 2.664 | 9.991 | 1.785
2019-06-18 20:47 | 222 | 2664 | 2.664 | 9.984 | 1.802
2019-06-18 21:02 | 222 | 2664 | 2.664 | 9.979 | 1.78
2019-06-18 21:17 | 221 | 2652 | 2.652 | 9.973 | 1.786
2019-06-18 21:32 | 222 | 2664 | 2.664 | 9.973 | 1.787
2019-06-18 21:47 | 222 | 2664 | 2.664 | 9.987 | 1.795
2019-06-18 22:02 | 222 | 2664 | 2.664 | 9.972 | 1.791
2019-06-18 22:17 | 221 | 2652 | 2.652 | 10.007 | 1.779
2019-06-18 22:32 | 222 | 2664 | 2.664 | 9.97 | 1.784
2019-06-18 22:47 | 222 | 2664 | 2.664 | 9.991 | 1.772
2019-06-18 23:02 | 222 | 2664 | 2.664 | 9.979 | 1.778
2019-06-18 23:17 | 222 | 2664 | 2.664 | 9.978 | 1.79
2019-06-18 23:32 | 222 | 2664 | 2.664 | 9.984 | 1.797
2019-06-18 23:47 | 221 | 2652 | 2.652 | 9.996 | 1.792
2019-06-19 00:02 | 222 | 2664 | 2.664 | 9.982 | 1.785
2019-06-19 00:17 | 221 | 2652 | 2.652 | 9.967 | 1.794
2019-06-19 00:32 | 222 | 2664 | 2.664 | 9.982 | 1.789
2019-06-19 00:47 | 221 | 2652 | 2.652 | 9.965 | 1.791
2019-06-19 01:02 | 222 | 2664 | 2.664 | 9.99 | 1.783
2019-06-19 01:17 | 222 | 2664 | 2.664 | 9.988 | 1.792
2019-06-19 01:32 | 221 | 2652 | 2.652 | 9.99 | 1.81
2019-06-19 01:47 | 221 | 2652 | 2.652 | 10.009 | 1.8
2019-06-19 02:02 | 222 | 2664 | 2.664 | 9.999 | 1.789
2019-06-19 02:17 | 222 | 2664 | 2.664 | 9.99 | 1.801
2019-06-19 02:32 | 222 | 2664 | 2.664 | 9.991 | 1.8
2019-06-19 02:47 | 222 | 2664 | 2.664 | 9.996 | 1.802
2019-06-19 03:02 | 221 | 2652 | 2.652 | 9.98 | 1.794
2019-06-19 03:17 | 222 | 2664 | 2.664 | 9.974 | 1.799
2019-06-19 03:32 | 222 | 2664 | 2.664 | 9.984 | 1.809
2019-06-19 03:47 | 222 | 2664 | 2.664 | 9.992 | 1.793
2019-06-19 04:02 | 222 | 2664 | 2.664 | 9.996 | 1.804
2019-06-19 04:17 | 222 | 2664 | 2.664 | 9.972 | 1.8
2019-06-19 04:32 | 222 | 2664 | 2.664 | 9.973 | 1.796
2019-06-19 04:47 | 222 | 2664 | 2.664 | 9.983 | 1.786
2019-06-19 05:02 | 221 | 2652 | 2.652 | 9.978 | 1.799
2019-06-19 05:17 | 222 | 2664 | 2.664 | 9.979 | 1.798
2019-06-19 05:32 | 222 | 2664 | 2.664 | 9.97 | 1.812
2019-06-19 05:47 | 221 | 2652 | 2.652 | 9.989 | 1.797
2019-06-19 06:02 | 222 | 2664 | 2.664 | 9.975 | 1.808
2019-06-19 06:17 | 221 | 2652 | 2.652 | 9.962 | 1.805
2019-06-19 06:32 | 221 | 2652 | 2.652 | 9.948 | 1.798
2019-06-19 06:47 | 221 | 2652 | 2.652 | 9.976 | 1.794
2019-06-19 07:02 | 221 | 2652 | 2.652 | 9.976 | 1.806
2019-06-19 07:17 | 221 | 2652 | 2.652 | 9.982 | 1.799
2019-06-19 07:32 | 221 | 2652 | 2.652 | 9.98 | 1.809
2019-06-19 07:47 | 221 | 2652 | 2.652 | 9.956 | 1.803
2019-06-19 08:02 | 220 | 2640 | 2.64 | 9.982 | 1.812
2019-06-19 08:17 | 220 | 2640 | 2.64 | 9.97 | 1.808
2019-06-19 08:32 | 220 | 2640 | 2.64 | 9.965 | 1.803
2019-06-19 08:47 | 145 | 1740 | 1.74 | 9.952 | 1.631
2019-06-19 09:02 | 101 | 1212 | 1.212 | 10.013 | 1.709
2019-06-19 09:17 | 119 | 1428 | 1.428 | 10.039 | 1.698
2019-06-19 09:32 | 117 | 1404 | 1.404 | 10.024 | 1.701
2019-06-19 09:47 | 116 | 1392 | 1.392 | 10.035 | 1.691
2019-06-19 10:02 | 115 | 1380 | 1.38 | 10.049 | 1.69
2019-06-19 10:17 | 116 | 1392 | 1.392 | 10.044 | 1.695
2019-06-19 10:32 | 115 | 1380 | 1.38 | 10.047 | 1.697
2019-06-19 10:47 | 114 | 1368 | 1.368 | 10.044 | 1.706
2019-06-19 11:02 | 114 | 1368 | 1.368 | 10.075 | 1.72
2019-06-19 11:17 | 114 | 1368 | 1.368 | 10.058 | 1.706
2019-06-19 11:32 | 114 | 1368 | 1.368 | 10.03 | 1.704
2019-06-19 11:47 | 113 | 1356 | 1.356 | 10.045 | 1.696
2019-06-19 12:02 | 114 | 1368 | 1.368 | 10.047 | 1.7
2019-06-19 12:17 | 114 | 1368 | 1.368 | 10.04 | 1.709
2019-06-19 12:32 | 113 | 1356 | 1.356 | 10.057 | 1.712
2019-06-19 12:47 | 113 | 1356 | 1.356 | 10.053 | 1.698
2019-06-19 13:02 | 113 | 1356 | 1.356 | 10.052 | 1.706
2019-06-19 13:17 | 112 | 1344 | 1.344 | 10.051 | 1.711
2019-06-19 13:32 | 113 | 1356 | 1.356 | 10.039 | 1.701
2019-06-19 13:47 | 112 | 1344 | 1.344 | 10.039 | 1.706
2019-06-19 14:02 | 113 | 1356 | 1.356 | 10.046 | 1.695
2019-06-19 14:17 | 112 | 1344 | 1.344 | 10.071 | 1.702
2019-06-19 14:32 | 113 | 1356 | 1.356 | 10.051 | 1.711
2019-06-19 14:47 | 113 | 1356 | 1.356 | 10.038 | 1.712
2019-06-19 15:02 | 113 | 1356 | 1.356 | 10.036 | 1.71
2019-06-19 15:17 | 113 | 1356 | 1.356 | 10.071 | 1.699
2019-06-19 15:32 | 113 | 1356 | 1.356 | 10.05 | 1.707
2019-06-19 15:47 | 113 | 1356 | 1.356 | 10.046 | 1.714
2019-06-19 16:02 | 113 | 1356 | 1.356 | 10.058 | 1.703
2019-06-19 16:17 | 112 | 1344 | 1.344 | 10.051 | 1.728
2019-06-19 16:32 | 113 | 1356 | 1.356 | 10.069 | 1.715
2019-06-19 16:47 | 112 | 1344 | 1.344 | 10.044 | 1.712
2019-06-19 17:02 | 113 | 1356 | 1.356 | 10.052 | 1.708
2019-06-19 17:17 | 113 | 1356 | 1.356 | 10.058 | 1.699
2019-06-19 17:32 | 113 | 1356 | 1.356 | 10.05 | 1.709
2019-06-19 17:47 | 113 | 1356 | 1.356 | 10.069 | 1.705
2019-06-19 18:02 | 113 | 1356 | 1.356 | 10.073 | 1.711
2019-06-19 18:17 | 113 | 1356 | 1.356 | 10.076 | 1.719
2019-06-19 18:32 | 113 | 1356 | 1.356 | 10.058 | 1.72
2019-06-19 18:47 | 114 | 1368 | 1.368 | 10.105 | 1.718
2019-06-19 19:02 | 112 | 1344 | 1.344 | 10.061 | 1.713
2019-06-19 19:17 | 113 | 1356 | 1.356 | 10.074 | 1.716
2019-06-19 19:32 | 113 | 1356 | 1.356 | 10.084 | 1.718
2019-06-19 19:47 | 114 | 1368 | 1.368 | 10.062 | 1.714
2019-06-19 20:02 | 113 | 1356 | 1.356 | 10.071 | 1.717
2019-06-19 20:17 | 113 | 1356 | 1.356 | 10.061 | 1.719
2019-06-19 20:32 | 113 | 1356 | 1.356 | 10.05 | 1.72
2019-06-19 20:47 | 113 | 1356 | 1.356 | 10.066 | 1.721
2019-06-19 21:02 | 113 | 1356 | 1.356 | 10.072 | 1.737
2019-06-19 21:17 | 112 | 1344 | 1.344 | 10.072 | 1.71
2019-06-19 21:32 | 113 | 1356 | 1.356 | 10.092 | 1.72
2019-06-19 21:47 | 113 | 1356 | 1.356 | 10.072 | 1.709
2019-06-19 22:02 | 113 | 1356 | 1.356 | 10.078 | 1.731
2019-06-19 22:17 | 113 | 1356 | 1.356 | 10.069 | 1.709
2019-06-19 22:32 | 113 | 1356 | 1.356 | 10.071 | 1.713
2019-06-19 22:47 | 113 | 1356 | 1.356 | 10.075 | 1.723
2019-06-19 23:02 | 113 | 1356 | 1.356 | 10.07 | 1.726
2019-06-19 23:17 | 113 | 1356 | 1.356 | 10.084 | 1.738
2019-06-19 23:32 | 113 | 1356 | 1.356 | 10.075 | 1.728
2019-06-19 23:47 | 113 | 1356 | 1.356 | 10.085 | 1.718
2019-06-20 00:02 | 113 | 1356 | 1.356 | 10.064 | 1.724
2019-06-20 00:17 | 113 | 1356 | 1.356 | 10.08 | 1.72
2019-06-20 00:32 | 112 | 1344 | 1.344 | 10.073 | 1.722
2019-06-20 00:47 | 113 | 1356 | 1.356 | 10.078 | 1.733
2019-06-20 01:02 | 113 | 1356 | 1.356 | 10.056 | 1.731
2019-06-20 01:17 | 112 | 1344 | 1.344 | 10.077 | 1.725
2019-06-20 01:32 | 112 | 1344 | 1.344 | 10.093 | 1.729
2019-06-20 01:47 | 112 | 1344 | 1.344 | 10.101 | 1.731
2019-06-20 02:02 | 112 | 1344 | 1.344 | 10.078 | 1.729
2019-06-20 02:17 | 112 | 1344 | 1.344 | 10.096 | 1.746
2019-06-20 02:32 | 112 | 1344 | 1.344 | 10.08 | 1.724
2019-06-20 02:47 | 111 | 1332 | 1.332 | 10.069 | 1.727
2019-06-20 03:02 | 112 | 1344 | 1.344 | 10.075 | 1.728
2019-06-20 03:17 | 111 | 1332 | 1.332 | 10.061 | 1.727
2019-06-20 03:32 | 112 | 1344 | 1.344 | 10.059 | 1.729
2019-06-20 03:47 | 112 | 1344 | 1.344 | 10.064 | 1.721
2019-06-20 04:02 | 111 | 1332 | 1.332 | 10.083 | 1.73
2019-06-20 04:17 | 112 | 1344 | 1.344 | 10.064 | 1.742
2019-06-20 04:32 | 111 | 1332 | 1.332 | 10.08 | 1.735
2019-06-20 04:47 | 111 | 1332 | 1.332 | 10.078 | 1.733
2019-06-20 05:02 | 112 | 1344 | 1.344 | 10.066 | 1.739
2019-06-20 05:17 | 111 | 1332 | 1.332 | 10.082 | 1.734
2019-06-20 05:32 | 112 | 1344 | 1.344 | 10.084 | 1.741
2019-06-20 05:47 | 111 | 1332 | 1.332 | 10.072 | 1.746
2019-06-20 06:02 | 111 | 1332 | 1.332 | 10.069 | 1.731
2019-06-20 06:17 | 112 | 1344 | 1.344 | 10.065 | 1.736
2019-06-20 06:32 | 111 | 1332 | 1.332 | 10.057 | 1.723
2019-06-20 06:47 | 112 | 1344 | 1.344 | 10.068 | 1.745
2019-06-20 07:02 | 111 | 1332 | 1.332 | 10.059 | 1.731
2019-06-20 07:17 | 111 | 1332 | 1.332 | 10.044 | 1.735
2019-06-20 07:32 | 110 | 1320 | 1.32 | 10.035 | 1.735
2019-06-20 07:47 | 111 | 1332 | 1.332 | 10.037 | 1.726
2019-06-20 08:02 | 111 | 1332 | 1.332 | 10.065 | 1.741
2019-06-20 08:17 | 112 | 1344 | 1.344 | 10.073 | 1.73
2019-06-20 08:32 | 111 | 1332 | 1.332 | 10.035 | 1.742
2019-06-20 08:47 | 111 | 1332 | 1.332 | 10.071 | 1.729
2019-06-20 09:02 | 111 | 1332 | 1.332 | 10.043 | 1.747
2019-06-20 09:17 | 112 | 1344 | 1.344 | 10.052 | 1.738
2019-06-20 09:32 | 111 | 1332 | 1.332 | 10.027 | 1.732
2019-06-20 09:47 | 112 | 1344 | 1.344 | 10.067 | 1.748
2019-06-20 10:02 | 111 | 1332 | 1.332 | 10.061 | 1.742
2019-06-20 10:17 | 111 | 1332 | 1.332 | 10.045 | 1.751
2019-06-20 10:32 | 111 | 1332 | 1.332 | 10.043 | 1.742
2019-06-20 10:47 | 111 | 1332 | 1.332 | 10.044 | 1.743
2019-06-20 11:02 | 111 | 1332 | 1.332 | 10.023 | 1.743
2019-06-20 11:17 | 111 | 1332 | 1.332 | 10.038 | 1.757
2019-06-20 11:32 | 111 | 1332 | 1.332 | 10.053 | 1.752
2019-06-20 11:47 | 111 | 1332 | 1.332 | 10.046 | 1.746
2019-06-20 12:02 | 111 | 1332 | 1.332 | 10.054 | 1.741
2019-06-20 12:17 | 111 | 1332 | 1.332 | 10.05 | 1.757
2019-06-20 12:32 | 111 | 1332 | 1.332 | 10.047 | 1.754
2019-06-20 12:47 | 111 | 1332 | 1.332 | 10.047 | 1.75
2019-06-20 13:02 | 110 | 1320 | 1.32 | 10.036 | 1.755
2019-06-20 13:17 | 111 | 1332 | 1.332 | 10.042 | 1.746
2019-06-20 13:32 | 111 | 1332 | 1.332 | 10.063 | 1.767
2019-06-20 13:47 | 112 | 1344 | 1.344 | 10.051 | 1.756
2019-06-20 14:02 | 111 | 1332 | 1.332 | 10.047 | 1.756
2019-06-20 14:17 | 110 | 1320 | 1.32 | 10.052 | 1.755
2019-06-20 14:32 | 111 | 1332 | 1.332 | 10.056 | 1.762
2019-06-20 14:47 | 111 | 1332 | 1.332 | 10.043 | 1.77
2019-06-20 15:02 | 111 | 1332 | 1.332 | 10.049 | 1.749
2019-06-20 15:17 | 110 | 1320 | 1.32 | 10.044 | 1.75
2019-06-20 15:32 | 111 | 1332 | 1.332 | 10.048 | 1.744
2019-06-20 15:47 | 111 | 1332 | 1.332 | 10.035 | 1.762
2019-06-20 16:02 | 110 | 1320 | 1.32 | 10.069 | 1.768
2019-06-20 16:17 | 111 | 1332 | 1.332 | 10.05 | 1.765
2019-06-20 16:32 | 110 | 1320 | 1.32 | 10.086 | 1.762
2019-06-20 16:47 | 111 | 1332 | 1.332 | 10.044 | 1.764
2019-06-20 17:02 | 110 | 1320 | 1.32 | 10.047 | 1.769
2019-06-20 17:17 | 111 | 1332 | 1.332 | 10.061 | 1.76
2019-06-20 17:32 | 111 | 1332 | 1.332 | 10.052 | 1.768
2019-06-20 17:47 | 110 | 1320 | 1.32 | 10.069 | 1.754
2019-06-20 18:02 | 111 | 1332 | 1.332 | 10.044 | 1.763
2019-06-20 18:17 | 111 | 1332 | 1.332 | 10.064 | 1.767
2019-06-20 18:32 | 111 | 1332 | 1.332 | 10.064 | 1.75
2019-06-20 18:47 | 111 | 1332 | 1.332 | 10.057 | 1.764
2019-06-20 19:02 | 111 | 1332 | 1.332 | 10.093 | 1.772
2019-06-20 19:17 | 111 | 1332 | 1.332 | 10.073 | 1.779
2019-06-20 19:32 | 110 | 1320 | 1.32 | 10.069 | 1.762
2019-06-20 19:47 | 111 | 1332 | 1.332 | 10.061 | 1.759
2019-06-20 20:02 | 111 | 1332 | 1.332 | 10.087 | 1.774
2019-06-20 20:17 | 111 | 1332 | 1.332 | 10.072 | 1.757
2019-06-20 20:32 | 111 | 1332 | 1.332 | 10.064 | 1.779
2019-06-20 20:47 | 111 | 1332 | 1.332 | 10.078 | 1.768
2019-06-20 21:02 | 111 | 1332 | 1.332 | 10.072 | 1.766
2019-06-20 21:17 | 111 | 1332 | 1.332 | 10.061 | 1.778
2019-06-20 21:32 | 111 | 1332 | 1.332 | 10.066 | 1.77
2019-06-20 21:47 | 111 | 1332 | 1.332 | 10.067 | 1.774
2019-06-20 22:02 | 111 | 1332 | 1.332 | 10.078 | 1.764
2019-06-20 22:17 | 110 | 1320 | 1.32 | 10.075 | 1.771
2019-06-20 22:32 | 111 | 1332 | 1.332 | 10.078 | 1.768
2019-06-20 22:47 | 110 | 1320 | 1.32 | 10.049 | 1.765
2019-06-20 23:02 | 111 | 1332 | 1.332 | 10.084 | 1.774
2019-06-20 23:17 | 111 | 1332 | 1.332 | 10.064 | 1.768
2019-06-20 23:32 | 110 | 1320 | 1.32 | 10.075 | 1.785
2019-06-20 23:47 | 110 | 1320 | 1.32 | 10.055 | 1.779
2019-06-21 00:02 | 110 | 1320 | 1.32 | 10.052 | 1.788
2019-06-21 00:17 | 109 | 1308 | 1.308 | 10.056 | 1.77
2019-06-21 00:32 | 110 | 1320 | 1.32 | 10.08 | 1.782
2019-06-21 00:47 | 109 | 1308 | 1.308 | 10.064 | 1.782
2019-06-21 01:02 | 110 | 1320 | 1.32 | 10.076 | 1.779
2019-06-21 01:17 | 110 | 1320 | 1.32 | 10.086 | 1.781
2019-06-21 01:32 | 110 | 1320 | 1.32 | 10.079 | 1.781
2019-06-21 01:47 | 109 | 1308 | 1.308 | 10.068 | 1.786
2019-06-21 02:02 | 110 | 1320 | 1.32 | 10.081 | 1.777
2019-06-21 02:17 | 109 | 1308 | 1.308 | 10.082 | 1.787
2019-06-21 02:32 | 110 | 1320 | 1.32 | 10.069 | 1.77
2019-06-21 02:47 | 109 | 1308 | 1.308 | 10.054 | 1.781
2019-06-21 03:02 | 110 | 1320 | 1.32 | 10.066 | 1.787
2019-06-21 03:17 | 109 | 1308 | 1.308 | 10.074 | 1.777
2019-06-21 03:32 | 110 | 1320 | 1.32 | 10.078 | 1.78
2019-06-21 03:47 | 109 | 1308 | 1.308 | 10.061 | 1.78
2019-06-21 04:02 | 109 | 1308 | 1.308 | 10.054 | 1.782
2019-06-21 04:17 | 110 | 1320 | 1.32 | 10.053 | 1.779
2019-06-21 04:32 | 109 | 1308 | 1.308 | 10.073 | 1.779
2019-06-21 04:47 | 109 | 1308 | 1.308 | 10.071 | 1.776
2019-06-21 05:02 | 110 | 1320 | 1.32 | 10.056 | 1.792
2019-06-21 05:17 | 109 | 1308 | 1.308 | 10.052 | 1.782
2019-06-21 05:32 | 110 | 1320 | 1.32 | 10.077 | 1.796
2019-06-21 05:47 | 110 | 1320 | 1.32 | 10.081 | 1.777
2019-06-21 06:02 | 109 | 1308 | 1.308 | 10.061 | 1.793
2019-06-21 06:17 | 110 | 1320 | 1.32 | 10.081 | 1.786
2019-06-21 06:32 | 109 | 1308 | 1.308 | 10.077 | 1.792
2019-06-21 06:47 | 110 | 1320 | 1.32 | 10.056 | 1.786
2019-06-21 07:02 | 109 | 1308 | 1.308 | 10.072 | 1.789
2019-06-21 07:17 | 109 | 1308 | 1.308 | 10.052 | 1.791
2019-06-21 07:32 | 109 | 1308 | 1.308 | 10.055 | 1.787
2019-06-21 07:47 | 109 | 1308 | 1.308 | 10.035 | 1.788
2019-06-21 08:02 | 109 | 1308 | 1.308 | 10.058 | 1.794
2019-06-21 08:17 | 109 | 1308 | 1.308 | 10.079 | 1.79
2019-06-21 08:32 | 108 | 1296 | 1.296 | 10.044 | 1.788
2019-06-21 08:47 | 110 | 1320 | 1.32 | 10.073 | 1.792
2019-06-21 09:02 | 109 | 1308 | 1.308 | 10.054 | 1.792

## Meter Readings
Existing Sources Meter Readings
Date | Time | BH1 meter | BH1 (m3/d) | Spring meter | Spring flow (m3/d) | BH4 meter | BH4 flow (m3/d)
2019-06-10 | 7:17 | 57966 |  | 49838 |  | 5293
2019-06-11 | 8:20 | 58018 | 49.8204 | 49882 | 42.1557 | 5326 | 31.6168
2019-06-12 | 8:50 | 58076 | 56.8163 | 49929 | 46.0408 | 5358 | 31.3469
2019-06-13 | 8:06 | 58120 | 45.3868 | 49972 | 44.3553 | 5389 | 31.9771 | Test Pumping Monitoring Period
No readings
2019-06-17 | 7:38 | 58288 | 42.2052 | 50137 | 41.4515 | 5463 | 18.5904
2019-06-18 | 7:04 | 58327 | 39.9431 | 50168 | 31.7496 | 5494 | 31.7496
2019-06-19 | 7:52 | 58378 | 49.3548 | 50204 | 34.8387 | 5528 | 32.9032
2019-06-20 | 7:05 | 58438 | 62.0244 | 50236 | 33.0797 | 5543 | 15.5061
Test Pumping took place 15/06/19 to 17/06/19
Average abstraction / Spring flow rates over the testing period were as follows:
|  |  | BH1 (m3/d) |  | Spring flow (m3/d) |  | BH4 flow (m3/d)
|  |  | 42.2052 |  | 41.4515 |  | 18.5904