## Cover-sheet
Menter Môn Comments on NRW Request for Further Information and Stakeholder Consultation Responses
Applicant: Menter Môn Morlais Limited
Author: Various
Morlais Document No.: | Status: | Version No.: | Date:
MMC599 MOR-RHDHV-DOC-0170 | Final | 1 | 2021-02-19
© 2021 Menter Môn | This document is issued and controlled by: |  |  | Menter Môn
Morlais, Menter Môn. Registered Address: Llangefni Town Hall, Anglesey, Wales, LL77 7LR, UK
Unauthorised copies of this document are NOT to be made
Company registration No: | 3160233 | Requests for additional copies shall be made to Morlais Project

## NRW Licencing
| NRW Comments | MM Response
| We draw your attention to the response from the Maritime and Coastguard Agency (MCA) (2 September 2020) which states how they are unable to provide comment upon the marine licence application until the updated Navigation Risk Assessment (NRA) and revised EIA chapter have been formally submitted. Although we welcome the submission of the updated NRA and EIA Shipping and Navigation chapter, as received on 30 September 2020; this new information was not consulted upon during the second round of consultation which commenced on 22 July 2020 and closed on the 2 September 2020. | Through the TWAO process the MCA have reviewed and commented on the NRA Addendum (NRAA) and the updated ES Chapter. We believe that we have addressed the majority of their comments either through the issuance of these revised documents or through the TWAO Public Inquiry process.
| Following the second round of consultation responses you will note a number of concerns which must be addressed and/or clarified. It is strongly recommended that you review and respond accordingly to all the points raised by the various consultees during the second consultation round. Within this letter specific attention is given to a number of the clarification points and responses, of which many will need to be addressed before the marine licence process progresses. However, this list is not exhaustive and consideration must be made to all the consultee comments. As done previously, a signposting matrix and relevant supporting documents should be provided to allow cross-referencing against the responses. | Responses are provided to stakeholder consultation responses throughout the tabs of this spreadsheet
1. General Comments
| A recurring comment made by the consultees relates to the clarity around the Project Design Envelope (PDE) and, in particular, detail on the first phase (Phase 1). While it is appreciated that a Rochdale Envelope approach is required by this proposal, limiting the initial scale of deployment is considered a key mitigation measure and is presented as such within the outline Environmental Mitigation and Monitoring Plan (oEMMP). The oEMMP details that the first phase will be at an installed capacity at which no significant impact is predicted on marine mammals and diving birds as determined through modelling outputs. However, NRW Advisory have significant concerns on the reliance on modelling outputs alone in defining the initial phase. Acknowledging the reduced scale required to reduce uncertainty and provide necessary confidence that adverse ecological effects will be avoided during Phase 1; greater detail must be provided to clearly define the scale of initial deployment. Narrowing the scope would strengthen confidence in the assessments and address concerns raised by multiple consultees. Currently, we do not consider that you have adequately defined Phase 1. | As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148: https://www.dropbox.com/s/ss3831dg1rszuqg/Morlais%20Closing%20-%20NRW.pdf?dl=0] further progress has been made during the course of the Inquiry, including updates to the oEMMP and draft conditions. As concluded in NRW closing paragraph 37: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision-maker that there would be no such adverse effect."
We have engaged with you on several occasions around the oEMMP, including an overview of our concerns (5 June 2020) and attendance at several meetings (12 June 2020; 26 June 2020) and acknowledge that further information has been provided. However, we still have significant concerns about the lack of detail within the oEMMP. We expect the comments made by the consultees during the second round of consultation to be further considered.
| Assurance is made within the oEMMP to produce appropriate trigger points for marine mammals. However, commitment and detail on the trigger points and their implementation must be provided at this stage to understand how these would trigger action in real time and link to a rapid response to prevent possible collisions and an adverse effect from occurring. We also highlight the need for a greater level of detail on the monitoring and mitigation measures for marine mammals and seabirds. There is still considerable uncertainty on the effectiveness of some of the measures outlined. | Table 1-1 of the OEMMP provides an illustration of potential use of proximity trigger points in a detailed EMMP. The Advisory Group will oversee the development of detailed proximity trigger points with expert advice post consent. The Applicant has now reached agreement with NRW that the oEMMP will ensure there will be no adverse effect on marine mammals as a result of collision, as outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148] paragraph 38: "Insofar as NRW would have preferred the oEMMP to contain further detail on certain aspects, it accepts that these matters can be progressed further if and when the detailed EMMP is discussed in due course." This will include further discussions, details and agreements with regards to real-time trigger points, monitoring and mitigation methods.
| There is considerable reliance and referral to the Advisory Group (AG) within the oEMMP, despite its structure, responsibilities and way of working still needing to be agreed. This results in added uncertainty around the measures implemented to avoid adverse effects. We consider that the reliance and detail on the AG, within the oEMMP, must be removed in order to provide the necessary clarity and confidence on the measures proposed. We do, however, encourage you to engage with relevant stakeholder and experts throughout both the development and implementation of the EMMP. | The use of an Advisory Group to oversee an adaptive management approach to mitigation and monitoring of a marine energy project has considerable precedence in consented tidal energy projects, in particular SeaGen and MeyGen. In NRW’s guidance to marine developers (NRW,2020. Using adaptive management for marine developments. Guidance for marine developers) an Advisory Group “including you as a developer, regulators, advisors and key stakeholders” is identified as a useful mechanism for implementing and managing an adaptive management plan and providing appropriate governance. As outlined in the NRW closing [Inquiry Doc - 148] paragraph 39: "NRW would expect the extent of the required monitoring (for all species) to be agreed by the Advisory Group identified in the oEMMP."
2. Coastal Processes
| Acknowledging the complex modelling which has been used to derive the assessment conclusions can you confirm how monitoring will be carried out to validate the modelling. If no monitoring is being proposed you will need to provide justification for us to consider. | Pre- and Post- construction bathymetry surveys and Acoustic Doppler Current Profiling (ADCP) will be undertaken in the vicinity of devices for engineering purposes. Menter Mon would, in principle, be happy to work in collaboration with NRW to explore the potential for these surveys to be used to monitor coastal processes and the potential for collaborating with academic research. These proposals are proportionate to the potential low/negligible magnitude of effect in the near- and far-field, under the worst case scenario.
| We strongly recommend that clarification is given to how and where the findings from the coastal processes modelling are considered within the NRA and Shipping and Navigation chapter. | Please see section 9.1 page 68 of the NRAA which details how the findings from the coastal processes modelling are considered within the NRAA. This is then referenced in the Amended ES Chapter.
| Further information has recently been submitted in relation to the Holyhead Port Expansion marine licence application (ref; CML1931) and is available on our public register. Additional consideration should be given within the cumulative impact assessment to the potential inter-relationships with the Holyhead Port proposal from changes in hydrodynamics, waves and sediment pathways. | This issue has now been resolved through ongoing engagement with NRW. NRW stated in their response dated 27th November 2020 to FEI under the TWAO process: We had previously raised concerns that cumulative impacts with any of the Holyhead port proposals (which includes increased tonnage to Holyhead deep disposal ground) had been assessed as ‘no pathway to impact’. We have since reviewed the Supplementary Note (ref. PB5034-RHD-ZZ-XX-NT-Z-1008) provided by the applicant dated 18/11/2020. The note refers to the tidal current and sediment transport cumulative effects with Holyhead North disposal site. The applicant has changed the assessment conclusion from ‘no pathway to impact’ to ‘negligible impact’. We agree with the assessment of ‘negligible impact’ based on the information presented.
3. Marine Water and Sediment Quality
| We recommend that the potential impacts on marine water quality in relation to surface water runoff to the Beddmanarch Bay SFW and Holyhead Strait WFD waterbody be detailed within the Surface Water Drainage Strategy. This should include how the potential increases in suspended sediment and contaminants will be mitigated. | Beddmanarch Bay SFW and Holyhead Strait WFD waterbody are considered in the ES Appendix 8.1 Water Framework Directive Compliance Assessment Addendum (Document MOR/RHDHV/APP/00126a(3)). The runoff of sediment and contaminants from terrestrial construction and operational activities will be controlled by a suite of best practice mitigation measures embedded into the scheme design and secured through the requirement for a CoCP in accordance with the Outline CoCP which includes surface water and drainage (proposed Planning Condition 3 of the draft TWAO). These will prevent an increase in the supply of sediment and contaminants into the coastal water bodies that receive drainage from the onshore site, and therefore prevent any adverse impacts on the shellfish water or WFD waterbodies.
| Clarification should be provided on where background suspended sediment concentration (SSC) for the project area has been sourced. Likewise clarification is required surrounding the values used for volumes of sediment generated by foundation installation, see NRW Advisory response for further detail. | The 3-4mg/l background levels quoted in the Metocean and Physical Processes ES Supplementary Note are quoted in the Introduction of Ellis et al (2008) referring to the work by Bowers et al. (1998). Bowers, D.G., Boudjelas, S., Harker, G.E.L., 1998. The distribution of fine suspended sediments in the surface waters of the Irish Sea and its relation to tidal stirring. International Journal of Remote Sensing 19 (14), 2789-2805.
4. Benthic and Intertidal Ecology
| Continuing concerns have been raised around the potential to mitigate adverse effects on Section 7 features present within the MDZ. A strong reliance is placed on the possible micro-siting of devices and related infrastructure as a measure to avoid or reduce impacts; however, the feasibility of the approach is questioned by NRW Advisory. We strongly recommend that consideration is given to this issue along with commitment to carry out pre-construction surveys and deploy devices in a manner that minimises the potential impacts on Section 7 features. | Distribution of reef features identified via the EIA characterisation surveys was shown to be patchy and therefore micro-siting is expected to be sufficient to avoid these features throughout most of the MDZ. Although limitations such as the availability of tidal resource may preclude substantial changes in location, micro-siting of up to 100 m from initial locations is expected to be possible. In view of this spatial flexibility it is anticipated that the overall effect of the micro-siting mitigation will be sufficient to locate tidal devices away from Annex I and Section 7 habitats in most cases. However, in recognition that there may be occasions where micro-siting is not feasible, an Outline Marine Biodiversity Enhancement Strategy document has been prepared on behalf of Menter Mon and discussed with NRW Advisory specialists. This document provides details of mitigation that would be required to offset the potential loss of some of Annex I habitats and/or Section 7 features. Following several revisions to the document, an (Outline) document has been produced which is agreed with NRW Advisory. It is expected that any Marine Licence issued for the Project would include a condition to update this Outline document into a FINAL Marine Biodiversity Enhancement Strategy document.
| Subject to a positive determination the need to complete a biosecurity risk assessment and management plan would be required before the commencement of works. We acknowledge that an outline Invasive Non-native Species Management Plan was submitted with the application and recommend that the comments received in relation to INNS are considered as you develop this document. | Noted. The INNS Plan will be developed post consent in consultation with NRW
| Further information has recently been submitted in relation to the Holyhead Port Expansion (see above). Additional consideration should be given to the potential cumulative effects with the Holyhead Port proposal on benthic features. | A Supplementary Note has since been provided to NRW (dated 18/11/2020) which assesses the cumulative impacts with Holyhead Port Expansion, in light of an addendum submitted by the Holyhead project. This information is now provided in Appendix 1 to the CIA Addendum (document MORRHDHVDOC0133(02)). The Supplementary Note explains that the footprints of the effects of the two projects, which are adjacent to each other (the Holyhead North footprint of effect is to the west of the Project footprint), have little overlap from a sediment transport perspective. Hence, the sediment transport pathways cumulative impact is a negligible impact as a worst case scenario. Also, given that the suspended sediment concentrations at Holyhead North are predicted to disperse to within background levels between each disposal event, there would be little potential for cumulative impacts with the Project. On the basis of these conclusions and the definition of negligible provided in Table 7-8 of ES Chapter 7 'No discernible change in receptor condition', there is no potential for a discernible change in benthic ecology and therefore the cumulative impacts will, at worst be of negligible significance to benthic ecology.
5. Fish and Shellfish Ecology
| Consideration should be given to all the comments raised in relation to fish and shellfish. | On 20 October 2020, the applicant submitted a document entitled ‘Additional Information to Support Morlais Habitats Regulations Assessment (migratory fish)’ (ref: MMC 351 MOR-MSP-DOC-003). In addition, migratory fish have been added to the OEMMP. In their response dated 27th November 2020, NRW stated: "based on the new information presented by the applicant of no evidence of harmful interaction with devices from marine renewable sites elsewhere we are able to agree with the overall conclusion that there will be no adverse effect on site integrity as far as sites designated for fish species are concerned."
6. Marine Ornithology
| We recommend that further detail and full working is provided around the collision risk modelling calculations. This will provide greater confidence in the conclusions. | The CRM and ERM spreadsheets providing the full working were originally submitted to NRW in 2019. These were resubmitted on 16th November 2020 following the identification of an error which has been corrected.
| To provide confidence in the oEMMP and the assessments which have been made based on the outcomes of operational monitoring measures, the detail on monitoring and mitigation measures needs to be sufficient pre-consent. There is concern that some of the measures proposed in the oEMMP have not been tested and are still under development, therefore further information on these measures are required in the oEMMP. Examples include but are not limited to: monitoring collisions of diving birds with turbines; GPS tagging. | All of the monitoring methods Table 4-1 of the outline EMMP are in considered to be potentially applicable to the detailed EMMP. All possible monitoring and mitigation options identified in the outline EMMP will be reviewed and assessed for inclusion in the detailed EMMP. No monitoring or mitigation options have been discounted at this stage. Regarding the examples cited, it is noted that: • Monitoring of seabirds, including monitoring for collision, has been successfully undertaken by Nova Innovation at their site in Shetland; • A number of tagging options that could provide useful monitoring data exist, and this includes GPS and TDR (time depth recorder) tags. Discussion of tagging has been updated in Table 4-1 of the outline EMMP. Additionally, NRW Advisory noted in its closing submission to the TWAO Inquiry (provided to NRW Licensing by email 15/2/21), para 39 that “….so far as monitoring the potential impact of the proposal on birds is concerned (including the risk of diving birds colliding with the development), NRW considers the position to be set out adequately for the purposes of the oEMMP in paragraph 100 of the final draft.”
| It is important that the oEMMP can be referred to directly and relied upon to contain all relevant information to support the assessment of no adverse effect. Thus sufficient detail on monitoring and mitigation measures key to reducing adverse effects should be encompassed within the oEMMP. | The outline EMMP will not be developed into a detailed format until the technology to be deployed and the location for deployment are known. The outline EMMP takes account of the requirements of NRW in order to be confident of no significant adverse effect.
| As with marine mammals, careful consideration should be given against the monitoring requirements and likely data needs that would be required to ensure further deployments (phases) could potentially progress in a manner that is realistic to the continued development of the Morlais Project testing site. Comments provided by NRW Advisory suggest that it may take a number of years of data acquisition before moving to the next phase could even be considered. | This advice is noted. The appropriate use of monitoring methods and their application to monitoring questions and indicators will be a task for the Advisory Group during the development of the detailed EMMP. This will include pre and post deployment monitoring, as baseline requirements will form part of this judgement.
| A comment has been raised by NRW Advisory as to whether you plan on using the original baseline boat surveys or new vantage point type surveys to inform change in use of area by birds pre and post installation. Please provide clarification on this point. | As noted above, the appropriate use of monitoring methods and their application to monitoring questions and indicators will be a task for the Advisory Group during the development of the detailed EMMP. Some of the monitoring methods reviewed may be more or less appropriate depending upon the type of technology deployed and the location of deployment within the MDZ.
| Further engagement with NRW and RSPB is recommended on the continued development of the oEMMP. | The Applicant has engaged with RSPB and NRW on the OEMMP and will continue to do so during development of the detailed EMMP post consent
7. Marine Mammals
| In our letter dated 2 March 2020, it was recommended that the sensitivity categorisation for marine mammal species was revisited due to failure to incorporate location importance and value judgements into the impact assessment methodology. While we recognise your acknowledgment to NRW Advisory’s comment (22 May 2020), please note that this point has been raised and sensitivity categorisation questioned again by NRW Advisory during this second round of consultation. | As stated in section 12.4.4.2 of ES Chapter 12, all species of marine mammal have been considered to be high value and the value of each species is used, where relevant, to modify the sensitivity of each species. However, as outlined in Section 12.4.4.2, high value and high sensitivity are not necessarily linked. A receptor could be of high value but have a low or negligible physical/ecological sensitivity to an effect. Therefore, the species sensitivity has been taken into account in the assessments. This takes into account the individual receptors capacity to avoid the anticipated impact. In addition, an assessment of each marine mammal species has been completed based on the sensitivity value of each population within Welsh waters, as defined by Sparling et al. (2015), for context and comparison only, for the assessment of collision risk. The summary of the potential impacts on marine mammals in ES Table 12-108 takes into account the value and sensitivity combined. For collision risk with operation turbines this has been assessed as high for bottlenose dolphin and low for all other species, including harbour porpoise. However, if the value and sensitivity combined is assessed as high for harbour porpoise the overall residual impact could change from minor to moderate adverse. However, this does not take account of the mitigation secured through the EMMP which will ensure there will be no adverse effect on marine mammals from SACs. This has been agreed by NRW as stated in their closing to the inquiry: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect."
| Due to uncertainties on CRM/ERM, avoidance rates and other parameters there is not enough information to conclude that the scale of Phase 1, as broadly outlined within the oEMMP and other documents, represents sufficient mitigation to rule out AEOSI. We strongly recommend that consideration is given to a reduction in the scale of Phase 1 and a clearer more committed description of Phase 1 must be provided (see General Comments above). Currently, the description of Phase 1 is wholly defined upon the modelling outputs and hence there exists considerable uncertainty around the assessments made, particularly in relation to bottlenose dolphin. | See response to row 5 above
| Consequently, we consider that monitoring and additional mitigation are required during Phase 1. Details of the measures applied during Phase 1 and how these will reduce the potential for an adverse effect should be clarified within the oEMMP and across all other relevant documents. | See response to row 5 above
| The oEMMP details the intention to remove monitoring and mitigation requirements over the lifetime of the project. Monitoring will likely be required throughout the operational phase to detect any collisions and mitigation should be available in the event of a collision. | Revised wording in the outline EMMP has been discussed with NRW Advisory and para 39 now includes the following revised wording: “Note it is the Applicant’s proposal to remove monitoring and mitigation requirements as soon as evidence gained from the EMMP shows that it is appropriate to do so, with agreement of Regulators.”
| Further detail is required within the oEMMP on the implementation of trigger points and how these would trigger action in real time to prevent possible collisions and an adverse effect from occurring. It should be acknowledged in the oEMMP that a rapid response would be required even if a single collision is detected. | Plate 2-3 of the outline EMMP shows an outline process for incident management, which allows for real time monitoring. The figure reproduced in the plate was provided in advice from NRW Advisory (Natural Resources Wales (NRW), 2020. Advice on adaptive management of the risk of collision impacts on protected marine mammal species in Welsh waters from the Morlais Project. Dated 15/10/2020) for inclusion within the outline EMMP. The outline EMMP makes clear a commitment real time monitoring, in particular with reference to trigger points (para 70) and monitoring (Table 4-1).
| As detailed for seabirds, careful consideration should be given against the monitoring requirements and likely data needs that would be required to ensure further deployments could potentially progress in a manner that is realistic to the continued development of the testing site (see Marine Ornithology). | Plate 2-3 of the outline EMMP shows an outline process for incident management, which allows for real time monitoring. The figure reproduced in the plate was provided in advice from NRW Advisory (Natural Resources Wales (NRW), 2020. Advice on adaptive management of the risk of collision impacts on protected marine mammal species in Welsh waters from the Morlais Project. Dated 15/10/2020) for inclusion within the outline EMMP. The outline EMMP makes clear a commitment real time monitoring, in particular with reference to trigger points (para 70) and monitoring (Table 4-1).
| There exists significant concerns regarding the operational underwater noise assessments of turbines and Acoustic Deterrent Device’s (ADD’s). Clarification is sought on where these operational noise levels were sourced from, and whether it is realistic to assume that noise from the large rotor device will scale from the small rotor device. We also query whether these two source levels adequately consider the multiple different device types with potentially different noise characteristics. It is therefore not currently possible to assess whether the information presented is a realistic worst case. Furthermore, given the uncertainty over the accuracy of the information presented and the lack of information on the likely deployment and configuration of the ADD array, it is currently not possible to assess the likely impacts from ADDs. Further information is required to address these uncertainties. | There is a commitment in the oEMMP that the underwater noise from ADDs will be reviewed as part of the ongoing development of the EMMP to ensure there is no significant disturbance or adverse effects. There is also a commitment in the oEMMP that the mitigation methods will be proven to be effective prior to any tidal device operation. As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148] in relation to underwater noise including ADDS, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
| Detail surrounding the monitoring methods proposed in the oEMMP must be revisited to acknowledge the considerable uncertainties around how the monitoring will be implemented, and whether it will be effective. ADD’s should be considered as mitigation rather than monitoring and it is strongly recommended that the comments made on ADD’s by NRW Advisory are carefully acknowledged within the oEMMP including their configuration and deployment. | The current outline EMMP makes clear that monitoring methods will be reviewed during development of the detailed EMMP, to identify methods, indicators and monitoring questions appropriate to the technology deployed and the location of deployment. In response to advice from NRW Advisory, ADDs are identified clearly as mitigation throughout the outline EMMP (MMC447(2) MOR-RHDHV-DOC-0072 (09)). NRW Advisory states in its closing submission to the TWAO Inquiry (available at: https://www.dropbox.com/s/ss3831dg1rszuqg/Morlais%20Closing%20-%20NRW.pdf?dl=0), para 45: “The Applicant has included the commitments to monitoring and mitigation of underwater noise that NRW had suggested, incorporating NRW’s suggested text in a revision to para. 27 of the draft oEMMP ……”, and para 46 further notes that “NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage.”
| NRW Advisory have raised a concern around the approach used to assess barrier effects on marine mammals. Please clarify accordingly. | Underwater noise during construction and operation, and the physical presence of the tidal arrays and underwater infrastructure, could have the potential to create a barrier effect, preventing movement or migration of marine mammals between important feeding and / or breeding areas, or potentially increasing swimming distances if marine mammals avoid the site and go around it. The assessment of any barrier effects will take account of the maximum potential area of (i) potential noise impacts and (ii) the tidal arrays and underwater infrastructure, in particular the predicted extent towards the coastline. The maximum duration of any barrier effects will also be considered. The maximum potential number of individuals that could be affected will be based on the relevant species density estimates and will be considered as a proportion of appropriate the reference populations. Barrier effects were not raised as an issue at the Inquiry, however, any potential barrier effects will be considered as part of the oEMMP.
| It is strongly recommended that further engagement is sought with NRW Advisory and JNCC regarding the monitoring and mitigation measures and how these would be implemented. | The Applicant has engaged with NRW on the OEMMP and will continue to do so during development of the detailed EMMP post consent
8. Onshore Ecology
| We recommend that careful consideration is given to INNS including the commitment to manage INNS (in particular those species highlighted by the consultation responses) within the biosecurity risk assessment before work begins. | The detailed procedures for limiting INNS will be developed post consent as this requires input from Contractors. An Outline Invasive Non-Native Species Management Plan (document MOR/RHDHV/DOC/0075) demonstrates the information that will be provided prior to construction. This will be secured through a Marine Licence condition.
| If trenching is required we strongly recommend that early consideration is given to NRW Advisory comments on permanent habitat loss of any vegetated seacliff habitat, noting that NRW Advisory have concluded that the effect on this qualifying feature would lead to AEOSI. | In the event that Menter Mon’s preferred option of installing cables at landfall using HDD is not technically feasible due to engineering constraints encountered during the drilling, then cables would be installed on the cliff face using J-Tubes (‘Option 2’, as outlined in the Terrestrial Ecology Update v04 (Document MOR-RHDHV-DOC-0110(4))). As outlined in Section 9.3 of the Terrestrial Ecology Update v04, it remains Menter Mon’s position that in this situation the effects on SAC habitats would be small scale, long-term temporary and reversible following the lifetime of the project, and that due to the localised nature of the effects and the dynamic nature of the habitats involved this loss would constitute a ‘de minimis’ effect on the SAC only, and not give rise to AEOSI (in line with the principles of the SAC Management Plan). This position is set out in detail in Section 9.3 of the Terrestrial Ecology Update v04. The Applicant has proposed a planning condition (document) to the TWAO which states: "No works which comprise the installation or laying of cables externally up the cliff face at the proposed landfall shall be undertaken until: a. A written report has been submitted and approved by the Local Planning Authority explaining why it is not feasible for such cables to be installed by horizontal directional drilling or other trenchless technique. The report shall include details of testing and previous attempts at such installation and the reasons (if any) why those attempts have been unsuccessful. The report shall also include or be accompanied by a certification from a suitably qualified independent engineer, who has been agreed in writing with the Local Planning Authority prior to appointment, that the approach taken to testing and attempting to use horizontal directional drilling or other trenchless techniques meets normal industry standards"
9. Seascape and Landscape
| As noted by Isle of Anglesey County Council (IoACC) the Device Deployment Protocol should consider the cumulative effects of deployments on seascape and landscape. | The continual requirement to undertake a specific seascape, landscape and visual impact assessment for each deployment of tidal energy devices as part of the Device Deployment Protocol will ensure continual review and monitoring of the Project during the construction phase.
In relation to NRW Advisory’s comment, can you confirm your commitment to monitoring the effects of development within the seascape on the AONB.
| Further detail should be provided around the lighting requirements for construction/support vessels and this should be assessed accordingly, particularly in relation to the potential effect on the Anglesey AONB. | The number of construction vessels expected to be present was described in Document MOR/SLR/DOC/0001: Seascape Landscape and Visual Impact Assessment – Post Application Consultation Responses. The main construction and support vessels that would be present during the 10 year construction phase are those involved in inter-array cable installation (30.14% of the year), hub installation (49.32% of the year) and tidal device installation (throughout the year, with the potential for two additional vessels for 18% of the year). Therefore, it is expected that up to six vessels would be involved in these activities at any one time but there is potential for additional vessels to be present at any particular time (an expected maximum of 16 vessels). Additional vessels could comprise those involved in the installation of the cable tail and export cable and the installation of protection. However, the vessels involved in these activities are expected to be present for short parts of a given year during the construction phase; 5.48% (cable tail installation), 5.48% (export cable installation) and 3.29% (export cable protection installation). Overall, the expected maximum number of construction/support vessels that could be on site at any one time is 16. However, this concentration of vessels would only be present for a short part of the year and is also based on a worst-case scenario of the whole 240 MW being installed in one phase. As the construction would be based on a phased development a much lower number of vessels on site at any one time is likely to occur with breaks in activity between phases. The number of vessel days on site stated in the Environmental Statement is based on 24 hour working. Therefore, the vessel numbers stated above could be applicable at night (with associated lighting). It is possible that fewer vessels (than stated above) would operate at night as safer working conditions would occur during daylight hours, but it is not possible to be definitive about this as the detailed approach to installation will be developed by specialist contractors much closer to actual offshore works commencing. The judgements included in the SLVIA are based on full deployment of the devices assumed as part of the site design envelope throughout the operational phase. This comprises 130 surface emergent tidal energy devices and eight electrical hubs, concentrating on the main offshore components of the project. The SLVIA also assumed visibility of navigation lights on all the tidal energy devices with a visibility of not less than five nautical miles. However, subsequent consultation with Trinity House has meant that the lights on the tidal energy devices can be limited to 150m (i.e. less than the distance to the coastline).
Significant effects were predicted at the closest light time viewpoints within the Anglesey AONB (Car Park at South Stack Light House and Ellin’s Tower). Beyond these viewpoints the potential effects reduced due to a combination of the intervening distance and the baseline context. These predicted effects took account the overlap between the construction phase and the operational phase, together with the likely presence of construction and service vessels at night. If necessary, further detail would need to be provided in relation to device specific deployments, when more information is known about construction requirements.
| We note that IoACC requires the securing of adequate compensation measures, including enhancement of features, to balance the effects of adverse impacts of the project as confirmed in the ES on Seascape, Landscape and Visual receptors. The compensation package should be developed in agreement with IoACC and NRW Advisory. | Menter Môn has made a commitment to a landscape enhancement package for the AONB. A Section 106 Agreement for securing has been agreed with IoACC. This provides an incremental fund, based on the MWs deployed, which will be provided to IoACC for implementing landscape enhancements. The specific enhancements are not described in the Section 106 Agreement, although examples are stated. NRW could be involved in how this compensation package is delivered.
| It is strongly recommended that the varied comments made by NRW Advisory in relation to the content of the Outline Landscape and Management Plan (OLMP) are clarified and additional detail provided, as required. This includes the renaming of the OLMP to include ‘seascape’ in the title. | The Landscape Management Plan is currently an outline document. It has always been intended that this comprises a live document and would be added to. It will evolve as the Project moves forward and more detail on the construction phase becomes available. Seascape was not included in the title as it primarily covers terrestrial components of the Project. This title has been used throughout the consenting process including in the TWAO process. Changing the title now is likely to cause confusion. In addition the Device Deployment Protocol will deal with seascapoe effects as a result of the offshore elements of the projects. Menter Môn intend to update this document post consent and will discuss and agree required amendments to this document with NRW and IoACC as part of this process.
| Clarification is required to address how consideration has been given to assessing the increased visibility of surface emergent structures during spring tides. | The SLVIA is based on a sea level that reflects lowest astronomical tide. The majority of surface emergent structures that have been included in the Project Design Envelope are floating, therefore the same height of structures would be visible regardless of tide level.
10. Socio-economics, Tourism and Recreation
| The implications of losing and/or significantly restricting a recognised boating area should be assessed with consideration against the Sector Supporting Policy T&R_01b of the WNMP, in addition to the general policies such as SOC_01 and SOC_02. | The MDZ does not restrict safe access to the vast majority of recreational users, as shown by the NRA Addendum (Document MOR/RHDHV/APP/0030(3)). The Applicant maintains that the WNMP, including SOC_01 'Access to the marine environment', SOC_02 'Proposals that contribute to the well-being of coastal communities are encouraged' and T&R_01b 'opportunities to define areas of future opportunity for tourism and recreation' has been given due consideration in light of the absence of significant impacts on recreational boating, combined with the benefits of renewable energy development associated with reduced impacts to well-being as a result of climate change.
| Clarification should be given to support why the Supplementary Tourism and Recreation Assessment did not encompass interviews with RYA affiliated clubs in the area, nor did it consider training or cruising activity. | A response is provided in document MMC600 MOR-MM-DOC-0024
| We expect the applicant to provide justification around the approach to assessing the economic importance of marine tourism and recreation, in particular why consideration against the recommendations of the Seabed User and Developer Group (SUDG) have not been demonstrated. | A response is provided in document MMC600 MOR-MM-DOC-0024
| A number of objections on the tourism assessment were received which specifically question the approach and methodology. These should be considered and justified, as required. | A response is provided in document MMC600 MOR-MM-DOC-0024
11. Navigation
| As noted above (General Comments), the updated Navigation Risk Assessment (NRA) and EIA Shipping and Navigation chapter were received on 30 September 2020. This information was received following the closing of the second round of consultation and thus has not been consulted upon. Therefore, it should be acknowledged that the comments in this section are based upon earlier versions of these documents. | Noted. Some of our responses below are based on comments from consultees received through the TWAO process.
| During the second round of consultation a number of concerns were raised upon the quality and content of the information used to inform the NRA and EIA navigation chapter. These encompassed but are not limited to: • Failure to consider all possible maritime safety impacts to recreational craft • Not including data covering the peak recreational period • No consideration of non-AIS equipped recreational craft • Failure to follow MGN 543 leading to an incomplete and inaccurate NRA • Not assessing the full implications of the MDZ on recreational boating • Failure to apply the Rochdale Envelope in a manner which aligns with guidance | The specific points rasied are addressed below but it is also worth noting that progress has been made with the RYA who, through their TWAO Public Inquiry Closing, advised that of four main concerns three had now "fallen away" namely: 1. The design options had not been finalised, making it impossible to assess the full impact of the project on recreational boating activity; 2. The Navigation Risk Assessment (and its Addendum) and the Interactive Boundaries Assessment did not comply with MGN543; 3. The Navigation Risk Assessment (and its Addendum) and Interactive Boundaries Assessment apparently relied exclusively on AIS and radar data to provide information about boating activity in the vicinity, which risked overlooking the significant proportion of recreational boats which do not carry AIS and offer a small radar silhouette; • Failure to consider all possible maritime safety impacts to recreational craft The purpose of an NRA is to capture and describe all navigation hazards associated with a project and to define, quantify and rank the subsequent risks associated. This is all described in detail in Annex A of the NRAA. A key part of the NRA is also data gathering and stakeholder consultation the details of which are also clearly outlined in the NRAA. The NRAA does consider all recreational users and considers a wide range of impacts on those users. • Not including data covering the peak recreational period The MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements." With regard to the question of the timing of data acquisition, consultation with recreational stakeholders indicated that July and August through to the August Bank Holiday were the busiest period for users. The 2017 summer survey commenced on the August Bank Holiday weekend and so is representative of this busy period. • No consideration of non-AIS equipped recreational craft Once again we would highlight that the MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements." 28 days of surveys including AIS, RADAR and Visual surveys were completed between August and September 2017 and in April 2019. Through the course of the TWAO process it was firmly established that visual surveys were completed and the results incorporated into the NRAA and this was acknowledged and agreed by the MCA and RYA. • Failure to follow MGN 543 leading to an incomplete and inaccurate NRA The MCA have advised on numerous occasions that the NRA has been completed in accordance with MGN543. In their closing statement for the TWAO Public Inquiry the RYA stated that "Similarly, the MCA has since confirmed that, in its view, the applicant had done all that was required of it under MGN543 so our objection in this regard has also fallen away." So we believe that this has been addressed. • Not assessing the full implications of the MDZ on recreational boating The two full NRAs completed by the applicant followed the FSA methodology approved by the IMO, and are considered compliant with MGN 543 as agreed by the MCA. • Failure to apply the Rochdale Envelope in a manner which aligns with guidance The Rochdale Envelope or PDE approach taken by the applicant was examined in detail in the TWAO Public Inquiry and the RYA did not challenge the evidence given on this topic. The ‘Rochdale Envelope’ approach is employed where the nature of the Proposed Development means that some details of the whole project have not been confirmed (for instance the precise number and/or location of structures) when the application is submitted, and flexibility is sought to address uncertainty. To allow for future developments and innovations in the type and nature of tidal energy devices that may be deployed across the site the NRA and ES considered a “worst case” scenario where any type of device, floating, subsurface of seabed mounted could be deployed across any part of the development site. Note that the proposed ML Conditions would require an array specific NRA to be undertaken before any new deployment which would then necessarily consider the detailed parameters of the proposed array in the specific location, and also with respect to any previously installed arrays. In additon the project is committed to updating the overarching site NRA every two years to monitor any changing circumstances.
| We would expect you to consider the above concerns. It is strongly recommended that you review and respond accordingly to all the points raised in the consultation and ensure that the documentation provided on the 30 September 2020 addresses these concerns. | Noted
| In relation to safety impacts on recreational craft, we require further justification why a discrete hazard assessment for kayakers has not been carried out within the NRA and is not considered within the EIA chapter. Such an assessment would consider the effects of hydrodynamic changes upon recreational boating (including kayakers) and the risk to kayakers of being swept into the MDZ and surface emergent devices. | Kayakers and unpowered craft were considered in the original NRA. However, following design changes and comments from stakeholders a further NRA, the NRA Addendum (NRAA), was undertaken. This included separating out powered and unpowered Recreational Vessels for clarity. Unpowered craft included sailing dinghies, kayas, canoes, rowing boats, SUPs etc. In addition, the NRAA further assessed risk to unpowered craft including swamping and capsizing and contact with devices. Finally, the NRAA also looked at the effects of tides, tidal streams and weather on all vessel types, including unpowered recreational craft in accordance with MGN 4543 Annex 2.
| We require clarity surrounding the use of traffic data that was more than 12 months out of date at the time of the Marine Licence application submission, and defining the ‘peak’ period for recreational boating as occurring from the end of August into September. | MGN543 states "An up to date, traffic survey of the area concerned should be undertaken within 12 months prior to submission of the Environmental Statement." but it goes on to say "However, if deemed necessary, to cover seasonal variations, peak times or perceived future traffic trends, the survey period may be extended to a maximum of 24 months." The MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements." With regard to the question of the timing of data acquisition, consultation with recreational stakeholders indicated that July and August through to the August Bank Holiday were the busiest period for users. The 2017 summer survey commenced on the August Bank Holiday weekend and so is representative of this busy period.
| As things progress, it is strongly recommended that further engagement with MCA and RYA is sought to discuss navigation risk and their respective concerns. We recommend that the outcomes of any such engagement are communicated to NRW. | The applicant has agreed a Statement of Common Ground with the MCA and Trinity House. We have also provided the RYA with a Statement of Common Ground which they have recently commented on. The applicant will continue to engage further with the RYA to see if this Statement of Common Ground can be agreed between the two parties. The applicant will also be seeking to enageg further with local sailors and sailing clubs.
12. Underwater Noise
| Clarification should be provided as to whether the Lofitech Seal Scarer can be considered a representative worst case scenario given that there are other known ADDs with higher source level. | See response to row 36 above
| Further information on the particular noise characteristics of the ADD that has been modelled (Lofitech Seal Scarer), such as the likely duration, rise-time, sound pressure impulse signature should also be provided. | See response to row 36 above
13. Cumulative Impacts
| Further evidence is required to justify why an in-combination air quality assessment is not considered necessary. | This issue has now been resolved through ongoing engagement with NRW. NRW stated in their response dated 27th November 2020 to FEI under the TWAO process: "we note that the applicant has explained that the predicted traffic flows will be significantly below the screening criteria and therefore no LSE are predicted (ref. MMC-188 MOR-RHDHV-DOC-0148, v.F1.0, 18/09/20). The applicant also confirms that there are no other major projects that are anticipated to increase traffic flows to result in the screening criteria being exceeded. The Holyhead Eco Park biomass facility, although granted permission, is currently on hold so there is no predicted overlap with the MDZ at present. The applicant confirms that if they were to overlap, the biomass facility would require an Environmental Permit to operate and would be required to meet specified emission limits to prevent significant impacts to receptors. We currently have no further comment to make on in-combination air quality impacts."
| Further information has recently been submitted in relation to the Holyhead Port Expansion (see above). Additional consideration should be given to the potential cumulative effects with the Holyhead Port proposal on benthic features. | This issue has now been resolved through ongoing engagement with NRW. NRW stated in their response dated 27th November 2020 to FEI under the TWAO process: We had previously raised concerns that cumulative impacts with any of the Holyhead port proposals (which includes increased tonnage to Holyhead deep disposal ground) had been assessed as ‘no pathway to impact’. We have since reviewed the Supplementary Note (ref. PB5034-RHD-ZZ-XX-NT-Z-1008) provided by the applicant dated 18/11/2020. The note refers to the tidal current and sediment transport cumulative effects with Holyhead North disposal site. The applicant has changed the assessment conclusion from ‘no pathway to impact’ to ‘negligible impact’. We agree with the assessment of ‘negligible impact’ based on the information presented.
| A number of inconsistencies and gaps have been identified by NRW advisory in relation to the cumulative and in-combination effects, such as the lack of consideration of developments within and around Holyhead. These require revisiting, consideration and inclusion, as relevant, before a robust conclusion can be made on the potential effects. It is recommended that the CIA screening matrix and CIA addendum are updated to ensure alignment with all documents, including HRA and WFD, where appropriate. Any changes and justifications should be clearly outlined in a signposting document | A revised CIA matrix and addendum are provided with this submission which aim to address NRW's comments regarding the CIA presented in the ES. The Applicant maintains that the plans and projects screened into the HRA and ES will not necessarily be consistent as the HRA considers connectivity of receptors from the designated site rather than directly with the Morlais Development Zone.
14. Documents requiring approval
| Within the application and supporting information as well as responses from consultees, a number of references are made to documents which are intended to be submitted for approval prior to commencement of works. These include but are not limited to, DDP, deployment specific NRA and CEMP. We recommend that a comprehensive list of these documents is provided. | The following plans are proposed: Cable Management Plan Installation Methodology Construction Environmental Management Plan Decommissioning Programme Device Deployment Protocol Environmental Mitigation and Monitoring Plan Marine Mammal Mitigation Protocol Pollution Prevention and Management Plan Updated Navigational Risk Assessment Operations and Maintenance Plan Written Scheme of Investigation (WSI) Aids to Navigation Plan Chemical Risk Assessment Invasive Non-native Species Management Plan
| We would also request clarification of where a single document is being proposed to cover the project or where separate documents are being proposed for each deployment. | The plans must be agreed prior to each deployment. This will entail a review of plans agreed for previous deployments to confirm they remain applicable or updates as required to ensure the plans are applicable to each deployment.
| For documents which cover both the marine and terrestrial area, such as the biosecurity risk assessment and management plan it would be useful to understand whether it is proposed that a single document is developed, or separate documents for the marine and terrestrial aspects of the proposal. | The scope of each plan would be agreed post consent with the relevant authority. It is likely that most plans will be separated by offshore and onshore to recognise the different stakeholder personnel that will be involved in the review of offshore and onshore plans.
| Reference is also made within supporting documentation to a Marine Mammal Mitigation Protocol, please could you clarify the relationship between this document and the EMMP. | The OEMMP will mitigate impacts on marine mammals to ensure no AEOSI on SACs focussing on collision risk with operational turbines and disturbance effects of underwater noise. A MMMP will ensure no injury of marine mammals during construction.

## FEI_ML009 NRW Advisory
FEI_ML009 ORML1938 – Consultation Response, NRW Advisory
Feedback | Response
Generally, our comments are made without prejudice to any further comments we may wish to make in relation to this application, the Transport and Works Act 1992 application, the Environmental Statement (ES), or other further evidence and documents provided by the applicant, NRW PS or other interested parties. Our comments are based solely on the information provided within the application documents to date. At the time of any further consultation there may be new information available which we will need to consider in making a formal response to NRW PS. | N/A
We have significant concerns with the proposed Marine Licence (ML) application. The application does not contain sufficient information to demonstrate that potential significant environmental effects will be appropriately avoided or mitigated. In our following comments we identify further information that should be provided by the applicant and/or matters that should be addressed prior to the determination of the ML application. We also identify conditions that, if applied to any ML consent, would mitigate the effect(s) in question. | See responses below
Since we provided our original comments on this ML application (date: 10/01/20, our ref: CAS-104373-N8Z1) we have engaged with the applicant via the Transport and Works Act (TWA) application on topics including marine mammals, marine ornithology, seascape, landscape and visual impact, terrestrial ecology, fish and marine/coastal processes in order to clarify and discuss the concerns raised in our representations on the TWA application. | N/A
On examining the additional information submitted for the ML application, we note and welcome that many of our previous concerns have been addressed. There are, however, still areas of concern that we believe require further consideration. In this response we seek to clarify where we are satisfied that the additional information has addressed our previous concerns and identify critical matters that we feel need to be addressed prior to the determination of the Marine Licence application. | See responses below
Our key concerns are summarised below, and our detailed comments are provided in Annex 1 of this letter. The following Table of Contents identifies the topics and locations of our detailed comments within Annex 1 based on their order within the ES and other supporting documents: | See responses below
NRW Advisory recognises the challenges associated with preparing a Project Design Envelope (PDE) for the project and the applicant’s intention to adopt a phased and adaptive management approach to consenting. We would welcome the opportunity to continue to provide advice to the applicant and NRW PS during the Marine Licence application process. | The Applicant welcomes ongoing engagement with NRW.
We advise that, without additional conditions, Adverse Effects on Site Integrity (AEOSI) due to collision impacts cannot be ruled out for the full 240MW project for any Special Areas of Conservation (SAC) with harbour porpoise, bottlenose dolphin, grey seal or harbour seal features within Welsh waters. We also consider that collision impacts cannot be ruled out for the Atlantic salmon feature of the Afon Gwyrfai a Llyn Cwellyn SAC. | The draft Marine Licence condition proposed by the Applicant (condition 38) includes "NRW must not approve any DEMMP unless it is satisfied that it provides such mitigation as is necessary to avoid adversely affecting the integrity of a European Site (as defined in The Conservation of Habitats and Species Regulations 2017 or The Conservation of Offshore Marine Habitats and Species Regulations 2017) to the extent that marine mammals or diving birds are a protected feature of that European Site". Therefore an AEOSI can be ruled out at this pre-consent stage as a result of this condition and the Applicants commitment to adaptive management to ensure there would be no AEOSI.
Whereas NRW Advisory does not object to an adaptive management approach in principle, the advice given on the draft EMMP proposals submitted are on a without prejudice basis on the assumption that the Competent Authority determines that an adaptive management approach is appropriate. Should the Competent Authority conclude that an adaptive management approach would not be appropriate for this project and that an adverse effect on the integrity of the Natura 2000 sites cannot be avoided, consent should only be granted if the Competent Authority is satisfied that there are no alternative solutions, imperative reasons of overriding public interest have been demonstrated, and that any necessary compensation will be secured. | The Applicant maintains that the adaptive management approach is appropriate and is in accordance with NRW's advice to Morlais on pre-consent assessment of collision risk and adaptive management, dated 13th May 2020.
We consider that a suitable adaptive management plan could in principle enable a conclusion of no AEOSI. We strongly recommend that conditions are applied which clearly define how the adaptive management plan will ensure collisions do not reach a level of AEOSI, and how that would be addressed if it occurred. However, there is currently considerable uncertainty over whether the proposed monitoring and mitigation will be deliverable and effective. NRW Advisory will advise further on any proposed adaptive management measures and in respect of the requirements of the Conservation of Habitats and Species Regulations 2017 as necessary during the ML application and TWA Inquiry processes. | As discussed above, a condition is proposed which ensures there will be no AEOSI.
It is currently not possible to assess the likely impact of disturbance to marine mammals from operational noise, due to the uncertainty about the range of potential impact and the accuracy of the information presented. It is also currently not possible to assess the likely impacts from Acoustic Deterrent Devices (ADDs) due to uncertainty over the accuracy of the information presented, and the lack of information on the likely deployment and configuration of the ADD array. | There is a commitment in the oEMMP that the underwater noise from operational turbines and ADDs will be reviewed as part of the ongoing development of the EMMP to ensure there is no significant disturbance or adverse effects. As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148] in relation to underwater noise, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
The worst-case scenario for cable trenching would involve a loss of Annex I habitat (Vegetated sea cliffs) from Holy Island Coast SAC. We cannot accept net loss of Annex I SAC habitat. Compensation may be possible through restoration of some areas of improved or semi-improved grassland along the cliff top, which would enhance the coastal ecosystem allowing the development of a more natural transitional zone between vertical cliff and more level grassland/heathland. Given the likelihood that some of the habitat enhancement may not be successful in this hostile environment and that it is not like-for-like replacement, we advise that a greater area than that to be lost should be allocated for enhancement. We would welcome further engagement in such discussions. | The Applicant maintains that given the small scale impacts on the cliff if HDD an AEOSI can be ruled out as detailed in the Terrestrial Ecology Assessment Update (document reference MMC189 MOR-RHDHV-DOC-0110). An Outline Habitat Enhancement Plan (document MMC578 MOR-RHDHV-DOC-0169) has now been agreed with NRW.
We consider that significant adverse residual effects upon daytime and evening views from the Anglesey Area of Outstanding Natural Beauty (AONB) remain, which in turn means that the public’s enjoyment of the AONB’s Special Qualities (expansive views/seascapes, and peace and tranquillity) would be significantly affected. We therefore maintain our significant concerns regarding the project. We advise that the residual impacts should be offset by developing and implementing an AONB landscape compensation package, in discussion and agreement with IoACC and NRW. | Acknowledged, the landscape compensation package is set out in the Section 106 Agreement.
An updated matrix with full reference to all plans and projects that have been considered within the Cumulative Impact Assessment (CIA) should be provided. This should be accompanied, as necessary, by an updated CIA addendum. Comments raised by the NRW topic specialists should also be addressed within the respective assessments, including the WFD compliance assessment. This will help to provide further confidence in an updated CIA. | An updated CIA matrix (Document MORRHDHVDOC0125(03) and CIA Addendum (Document MORRHDHVDOC0133(02)) are provided with this submission
Under section 6 of the Environment (Wales) Act 2016 (‘Biodiversity and resilience of ecosystems duty’), “a public authority must seek to maintain and enhance biodiversity in the exercise of functions in relation to Wales, and in so doing promote the resilience of ecosystems, so far as consistent with the proper exercise of those functions.” NRW Advisory considers that implementation of satisfactory mitigation measures would be essential to ensure that ecosystem resilience is maintained in the vicinity of the proposal. | An Outline Biodiversity Enhancement Plan (with regards to benthic ecology, document MMC555 MOR-RHDHV-DOC-0164) and an Outline Habitat Enhancement Plan (with regards to cliff ecology, document document MMC578 MOR-RHDHV-DOC-0169) have been agreed with NRW.
Annex 1: NRW Advisory Detailed Comments on Morlais Tidal Array Marine Licence application - additional information
1.0 Metocean Conditions and Coastal Processes | Noted
ES Volume I, Chapter 7
1. We consider that the additional information now allows for a considered appraisal of the impact conclusions reached on this topic.
2. A modelling suite of hydrodynamic, wave and sediment modelling has been completed for the known worst-case scenarios for coastal processes. We are confident that these can now be used to assess the project’s impact. | Noted
3. We are satisfied that, with the modelling carried out, the project’s zone of influence has now been assessed and all protected sites where changes in physical processes could be detrimental have been considered. | Noted
4. The baseline characterisation of suspended sediment, sediment regime and morphology have been greatly expanded upon, allowing an informed view on construction and operation scenarios. | Noted
5. We welcome that the applicant has avoided any footprint within the South Stack banner bank and therefore any direct impacts to this feature can be discounted. Bespoke sediment modelling has shown sediment pathways to be minimal and localised. | Noted
6. The worst-case wave modelling scenario has considered 60 floating devices in the southern permissible section of the array (which have an increased blockage effect on waves), 310 seabed-mounted devices and associated infrastructure. As advised in previous Technical Working Group (TWG) meetings with the applicant, this will constrain the project’s design as this is the worst case that has been assessed for this topic. | The submerged devices have a negligible effect on waves as shown in the results of the HRWallingford report (document MOR-HRW-DOC-0001) in particular Figures 5.42 - 5.47. For this reason there are no limitations (additonal to those already described in the PDE) placed on the number of submerged devices in the PDE owing to wave effects.
7. The clarification of the worst-case scenario for surface emergent devices (MOR/RHDHV/DOC/0143, 1.0, 22/05/20) is accepted. We note that the applicant does not believe a device limit should be a quantitative factor, rather the limit of 30MW per berth and the maximum of 4 berths being available within the southern section of the development zone. The worst case has been assessed in the modelling via the Orbital device, which has a greater hull length per MW than any of the other devices. | Noted
8. Our remaining comments following review of the additional information are summarised as follows: | N/A
9. There is currently no monitoring proposed for physical processes within the Outline Environmental Mitigation and Monitoring Plan (oEMMP). We would expect a development of this scale to ensure the conclusions of the Environmental Impact Assessment, which are based on complex modelling, are as predicted. We therefore recommend that the applicant proposes an appropriate monitoring plan in agreement with NRW, that will inform necessary management requirements thereafter. | Pre- and Post- construction bathymetry surveys and Acoustic Doppler Current Profiling (ADCP) will be undertaken in the vicinity of devices for engineering purposes. Menter Mon would, in principle, be happy to work in collaboration with NRW to explore the potential for these surveys to be used to monitor coastal processes and the potential for collaborating with academic research.
10. Cumulative impacts with any of the Holyhead port proposals (including increased tonnage to Holyhead deep disposal ground) have been assessed as ‘no pathway to impact’. We believe the developments and zones of impact are proximal and due to the assessments being based on complex modelling they should consider any inter-relationships from changes in hydrodynamics, waves and sediment pathways. We would therefore expect the project’s Cumulative Impact Assessment (CIA) to consider these projects further. | This issue has now been resolved through ongoing engagement with NRW. NRW stated in their response dated 27th November 2020 to FEI under the TWAO process: "We had previously raised concerns that cumulative impacts with any of the Holyhead port proposals (which includes increased tonnage to Holyhead deep disposal ground) had been assessed as ‘no pathway to impact’. We have since reviewed the Supplementary Note (ref. PB5034-RHD-ZZ-XX-NT-Z-1008) provided by the applicant dated 18/11/2020. The note refers to the tidal current and sediment transport cumulative effects with Holyhead North disposal site. The applicant has changed the assessment conclusion from ‘no pathway to impact’ to ‘negligible impact’. We agree with the assessment of ‘negligible impact’ based on the information presented."
Marine Water and Sediment Quality
ES Volume I, Chapter 8: Marine Water and Sediment Quality
11. Our remaining comments on marine water and sediment quality following review of the additional information are summarised as follows. | N/A
12. The Metocean and Physical Processes ES Supplementary Note, p. 14 (MOR/RHDHV/DOC/0111, F1.0, 25/03/20) has not considered the relevance of Beddmanarch Bay Shellfish Water (SFW) or Holyhead Strait WFD waterbody for water quality. Both the SFW and WFD waterbody are close to the Aluminium works where terrestrial, rather than marine, works would take place and polluted surface runoff could occur and affect marine water quality. We note that there will be a preferential selection of discharge methodology which will be included in a Surface Water Drainage Strategy (ES Volume I, Chapter 4: Project Description, p. 43, section 4.4.6.7 - MOR/RHDHV/DOC/0004, F4.0, Oct 2019); this should consider impacts on marine water quality, detailing how the potential increases in suspended sediment and contaminants will be mitigated in relation to surface water runoff to the Beddmanarch Bay SFW and Holyhead Strait WFD waterbody (Table 1.9 of the applicant’s WFD compliance assessment – MOR/RHDHV/APP/00126a, F4.0, 25/03/20). | The Metocean and Physical Processes ES Supplementary Note deals with changes arising as a result of the offshore works. Beddmanarch Bay SFW and Holyhead Strait WFD waterbody are considered in the ES Appendix 8.1 Water Framework Directive Compliance Assessment Addendum (Document MOR/RHDHV/APP/00126a(3)). The runoff of sediment and contaminants from terrestrial construction and operational activities will be controlled by a suite of best practice mitigation measures embedded into the scheme design and secured through the requirement for a CoCP in accordance with the Outline CoCP which includes surface water and drainage (proposed Planning Condition 3 of the draft TWAO). These will prevent an increase in the supply of sediment and contaminants into the coastal water bodies that receive drainage from the onshore site, and therefore prevent any adverse impacts on the shellfish water or WFD waterbodies.
13. The applicant has provided two further references which provide a more current description of the baseline conditions for the project area. However, peaks of 12mg l-1 are given in Ellis et al. (2008) compared to 10mg l-1 cited in the Metocean and Physical Processes ES Supplementary Note (MOR/RHDHV/DOC/0111, F1.0, 25/03/20). Robins et al. (2014) discussed in-situ measurements given by a piece of equipment called a LISST, which gives concentration as volume concentration (litres per litre) rather than mass concentration (e.g. mg l-1). A conversion can be applied using filtered water samples, but this has not been done. Figure 2.1 of the same document is from the Robins et al. paper and is for sediment transport (given as m² s-1) rather than sediment concentration (in either μl l-1 or mg l-1). Figure 2.1 shows the spatial variability in the maximum (as we previously requested clarity on the location) but does not show the baseline sediment concentration. Thus, we do not consider the Robins et al. reference appropriate given the lack of calibration and incorrect use of the figure in terms of suspended sediment concentration (SSC). However, the Ellis et al. paper does give limited evidence of concentrations. The “background levels” referred to in the Metocean and Physical Processes ES Supplementary Note (MOR/RHDHV/DOC/0111, F1.0, 25/03/20) are not given in either Ellis et al. or Robins et al. so we seek clarification on the source of these. | In this comment the clarification required is: The “background levels” referred to in the Metocean and Physical Processes ES Supplementary Note are not given in either Ellis et al. or Robins et al so we seek clarification on the source of these. The background levels quoted in the supplementary note were 3-4mg/l are quoted in the Introduction of Ellis et al (2008) referring to the work by Bowers et al. (1998). Bowers, D.G., Boudjelas, S., Harker, G.E.L., 1998. The distribution of fine suspended sediments in the surface waters of the Irish Sea and its relation to tidal stirring. International Journal of Remote Sensing 19 (14), 2789-2805.
14. In terms of suspended sediment generated by foundation installation drilling (Metocean and Physical Processes ES Supplementary Note, p. 6 - MOR/RHDHV/DOC/0111, F1.0, 25/03/20), the applicants state 117,780m³ of sediment will be released in total as a result of drilling for 290 devices. Each device is said to release 1020m³ of sediment, but 290 devices and 1020m³ sediment per device does not provide the total given. Footnote 1, page 6 of the same document indicates how the 117,780m³ value has been reached, so we seek confirmation of the applicability of the 1020m³ value. | 1020m3 is the worst case for a single device and 117,780m3 is the worst case for the project as a whole. As discussed in the ES Supplementary Note, due to the sequencing of construction it is not possible that the full 117,780m3 volume would all be released at the same time, therefore it is important to consider the maximum that could be released at any one time, i.e. 1020m3 for a single device or 2040m3 for concurrent installation.
15. The applicant also describes 1020m³ as the worst-case but explains that if there are two concurrent drillings the total will be 2040m³; we consider that this should be the worst case if it is possible for such a scenario to occur. However, we agree there will be little impact from the release of 2040m³ of sediment per tide due to the tidal mixing strength in the demonstration zone. The applicant has also assumed all the arisings would be fine sediment, whereas we advise they are likely to be mixed. | As above, 1020m3 is the worst case for a single device and 2040m3 is the worst case for concurrent installation, both have been considered.
3.0 Benthic and Intertidal Ecology
ES Volume I, Chapter 9
16. Our remaining comments following review of the additional information are summarised as follows. | See responses below
17. We consider that the impacts of development or activities on Annex I reef (including biogenic and bedrock/stony reef) habitat occurring outside SACs should be assessed and adverse effects minimised or mitigated as far as possible. However, the lack of specific benthic habitat survey information means that it is not possible to ascertain the scale and impact of the development on such habitats (as well as other habitats of conservation importance including those protected by section 7 of the Environment (Wales) Act 2016 and OSPAR). By the applicant’s own admission, micro-siting is only ‘likely’ to be possible as a mitigation measure, and “the ability to micro site Tidal Energy Converters (TECs) is more limited than for Offshore Wind Farms (OWFs)”. Therefore, considering the limited ability to adjust the placement of these devices, and the scale of what is proposed in relation to the availability of habitat, it is currently unclear as to whether the proposed micro-siting mitigation will be effective in minimising impact to Annex I/section 7 habitats. | The applicant agrees that 'undesignated' Annex I reef will be assessed with the same approach as designated reef. The Morlais marine habitat EIA characterisation surveys were conducted to obtain an understanding of the existing environment, including the range and extent of sensitive habitats of conservation importance. These data were then used as the basis of the assessment presented in the Morlais ES. The data produced from this survey has, in our opinion, achieved this objective. Certain Annex 1 habitat features recorded in the EIA characterisation survey, in particular biogenic reef such as Sabellaria spinulosa, is known to exhibit spatial and temporal variation. Therefore, closer to actual deployment of any project infrastructure, i.e. post-consent, a full Annex I reef survey and assessment will be conducted to inform pre-construction planning and consideration of any micro-siting that may be required to avoid any reef features. Distribution of reef features identified via the EIA characterisation surveys was shown to be patchy and therefore micro-siting is expected to be sufficient to avoid these features throughout most of the MDZ. Although limitations such as the availability of tidal resource may preclude substantial changes in location, micro-siting of up to 100 m from initial locations is expected to be possible. In view of this spatial flexibility it is anticipated that the overall effect of the micro siting mitigation will be sufficient to locate tidal devices away from Annex I habitats in most cases and reduce the significance of impacts on Annex I habitats from moderate to minor adverse. Therefore, the applicant maintains that the impact assessment for this receptor is correct. The applicant proposes a condition requiring micro-siting away from Annex I habitats as far as practically possible from an operational and tidal resource perspective to be included in any Marine Licence issued for the project. In addition, in recognition that there may be occasions where micro-siting is not feasible, an Outline Marine Biodiversity Enhancement Strategy document has been prepared on behalf of Menter Mon and discussed with NRW Advisory specialists. This document provides details of mitigation that would be required to offset the potential loss of some of Annex I habitats and/or Section 7 features. Following several revisions to the document, the Outline Marine Biodiversity Enhancement Strategy has been agreed with NRW. It is expected that any Marine Licence issued for the Project would include a condition to update this Outline document into a FINAL Marine Biodiversity Enhancement Strategy document.
18. We accept that the presence of Valued Environmental Receptor (VER) habitats in the predictive areas mapped within the project footprint is likely to be sparse. However, as the feasibility of micro-siting TECs, related infrastructure and cabling has not yet been determined there is uncertainty as to whether this approach will effectively avoid impacts to these habitats and this should be confirmed in advance of device deployment. We therefore advise that a condition to undertake pre-construction benthic and intertidal habitat surveys should be included with any consent to ensure that the location and extent of benthic and intertidal habitats of conservation importance are accurately assessed and the feasibility of the proposed micro-siting mitigation confirmed. | Noted, draft Marine Licence conditions include requirement for a further full Annex I reef survey and assessment at a higher resolution post-consent/pre-construction, and an additional condition requiring effects on Annex I habitats to be minimised through micro-siting as far as practically possible from an operational and tidal resource perspective.
19. Considering the overall 2.23km² direct benthic/intertidal footprint of the proposal (excluding indirect localised/microhabitat effects as a result of the device structures) and the limited evidence presented in relation to the assessment of direct and indirect habitat loss/degradation on Annex I habitat features and OSPAR/section 7 habitats, we are currently unable to agree with the assessment downgrading the impact from ‘moderate’ to ‘minor’ adverse as a result of post-consent mitigation measures, until the results of pre-construction surveys are available and the feasibility of micro-siting as a mitigation measure confirmed. Similarly, we have little confidence in the assessment of the scale of the potential impact on subtidal benthic and intertidal receptors as ‘low’. | The Applicant would be happy to accept (and expects) a condition requiring a further full Annex I reef survey and assessment at a higher resolution post-consent/pre-construction within any Marine Licence issued for this project. This will enable the full extent of Sabellaria spinulosa reef to be determined closer to actual installation works and will be used to inform the placing of infrastructure, highlighting areas which should be avoided entirely and areas where micro siting should be used to minimise impacts on protected habitats. These surveys will be conducted in line with Gubbay (2007) standards. The applicant commits that, as far as practical from an operational and tidal resource perspective, micro-siting will be used for the TECs and related infrastructure, as well as the cable route. It is expected that this commitment for micro-siting will be included in any future Marine Licence conditions. It is important to note that the ability to micro site tidal energy converters (TECs) is more limited than for offshore wind farms (OWFs), as TECs must be located where the tidal resource is available. However, as the distribution of reef habitat is patchy, micro-siting is likely to be possible throughout most of the MDZ. Therefore, adoption of this mitigation measure is expected to be sufficient to reduce the spatial extent, and thereby significance, of this impact from moderate to minor adverse. Although limitations such as the availability of tidal resource may preclude substantial changes in location, micro-siting of up to 100 m from initial locations is expected to be possible. In view of this spatial flexibility it is anticipated that the overall effect of the micro-siting mitigation will be sufficient to locate tidal devices away from Annex I and Section 7 habitats in most cases. As such, the determination of ‘low’ scale of impact is considered appropriate. As discussed above, an Outline Marine Biodiversity Enhancement Strategy has now been agreed with NRW. It is expected that any Marine Licence issued for the Project would include a condition to update this Outline document into a FINAL Marine Biodiversity Enhancement Strategy document prior to construction.
20. We acknowledge the worst-case scenario of cable landfall contributing to the overall total figure of 2.23km² of permanent benthic/intertidal habitat loss. Given the presence of Annex I habitat features, sub-features and section 7 habitats in the areas associated with the cable landfall we maintain that Horizontal Directional Drilling would be our preferred option. | HDD is also the Applicant's preferred option. The alternative of cable trenching at landfall must be retained in case HDD is not possible.
21. We advise that a biosecurity risk assessment and management plan is completed and implemented, to mitigate the risk of ingress and spread of marine invasive non-native species (INNS), for all project development activities, including construction, operation and decommissioning phases. This should also consider potential cumulative/in-combination effects with other marine licensable developments where an increase in shipping associated with construction activities may be concentrated around current hotspots for marine INNS. | Noted. The INNS management plan will be developed post consent in accordance with the outline plan (document MOR/RHDHV/DOC/0075) submitted with the application
22. The biosecurity risk assessment should acknowledge that there is a pathway for INNS from the Holyhead Port Expansion to interact in-combination with the Morlais proposal. The main potential risks associated with marine INNS will likely arise from the increased vessel and equipment use associated with the Holyhead port/marina. Increased vessel numbers and activity could potentially lead to increased spread of the Carpet Sea Squirt Didemnum vexillum and other high-medium risk INNS (which are defined in the Marine Invasive Non-native Species: Priority Monitoring and Surveillance List for Wales) to the project site and/or other areas. | The Applicant has committed to an INNS management plan to ensure it does not contribute to the transfer of INNS. The Applicant would expect that that such conditions would be imposed on other projects, including the Holyhead Port Expansion and therefore there would be no interaction/in-combination risk.
23. The biosecurity risk assessment and management plan should include consideration of all activities, vessels and equipment used as well as how the risk will be minimised through appropriate mitigation and adherence to best practice guidance and management measures. The biosecurity risk assessment should include a review of all available data on the presence of marine INNS where applicable to the proposal, and the potential risks associated with each species identified. Any further project-embedded mitigation measures should be led by the aforementioned documents. | The Outline Invasive Non-Native Species Management Plan (Document MOR/RHDHV/DOC/0075) demonstrates the information that will be provided in the final INNS which includes details on activities and vessels etc. In addition, the final plan must be agreed by the Regulators prior to construction. The Applicant expects this to be secured by Marine Licence condition.
24. Clarification is sought on the cumulative impact assessment (CIA) rationale as it is unclear how certain impact pathways have been considered and subsequently scoped out. We note that the submitted CIA review matrix (MOR-RHDHV-DOC-0125, F3.0, 07/03/20) has scoped out a potential impact pathway between subtidal benthic habitats and the proximal Holyhead Port Expansion due to there being ‘no pathway to impact’, but little justification for this has been given. Depending on the timing and phasing of the two developments, any potential increases in deposited dredged material at the Holyhead Deep licensed disposal ground from the construction and operation of the Holyhead Port Expansion could result in increased sedimentation on the habitats directly/indirectly affected by the Morlais project, causing further habitat degradation and reducing resilience and, potentially, the subsequent likelihood of recovery. We therefore advise that the project’s CIA considers these projects further (see also paragraph 10 above). | A Supplementary Note has since been provided to NRW (dated 18/11/2020) which assesses the cumulative impacts with Holyhead Port Expansion, in light of an addendum submitted by the Holyhead project. This information is now provided in Appendix 1 to the CIA Addendum (document MORRHDHVDOC0133(02)). The Supplementary Note explains that the footprints of the effects of the two projects, which are adjacent to each other (the Holyhead North footprint of effect is to the west of the Project footprint), have little overlap from a sediment transport perspective. Hence, the sediment transport pathways cumulative impact is a negligible impact as a worst case scenario. Also, given that the suspended sediment concentrations at Holyhead North are predicted to disperse to within background levels between each disposal event, there would be little potential for cumulative impacts with the Project. On the basis of these conclusions and the definition of negligible provided in Table 7-8 of ES Chapter 7 'No discernible change in receptor condition', there is no potential for a discernible change in benthic ecology and therefore the cumulative impacts will, at worst be of negligible significance to benthic ecology.
4.0 Fish and Shellfish Ecology
ES Volume I, Chapter 10
25. Most of our previous concerns regarding fish have now been addressed in the revised ‘Fish Ecology Issues: Responses to NRW comments’ document (MOR/RHDHV/DOC/0114, D2.0, 03/07/20). | Noted
26. The above document now acknowledges that migratory fish, including salmon, are likely to pass through the development area and therefore will be at risk of collision with deployed devices. This risk can be assumed to be highest for fish from the nearest SAC site of Afon Gwyrfai a Llyn Cwellyn. | Noted
27. Given the risk of collision we advise that migratory fish are included in the oEMMP (MOR-RHDHV-DOC-0072(03), F5.0, 03/07/20), which should include outline plans for monitoring collision and interaction of fish with devices. | Migratory fish are now included in the OEMMP (since version F6.0 dated 2nd November 2020)
5.0 Marine Ornithology
ES Volume I, Chapter 11
28. Our remaining comments following review of the additional information are summarised as follows.
Collision Risk Modelling (CRM) note (MOR/RHDHV/DOC/0115, F1.0, 25/03/20) | Agreed
29. The Collision Risk Modelling (CRM) note (MOR/RHDHV/DOC/0115, F1.0, 25/03/20) appears to provide adequate evidence to show that the populations of guillemots and razorbills at South Stack can still increase their populations during the proposed first phase of the project.
Outline Environmental Mitigation and Monitoring Plan (MOR-RHDHV-DOC-0072(03), F5.0, 03/07/20) | The Applicant maintains the expectation that the Regulator will consult the Advisory Group is made sufficiently clear throughout Section 3 of the OEMMP (document MMC447 MOR-RHDHV-DOC-0072 (09)).
30. Page 1, para. 6 states “Device deployments will only be allowed at scales at which regulators agree that the best available scientific understanding does not predict adverse impacts upon marine mammals or diving seabirds.” There has been previous discussion (TWG meeting held on 29 November 2019) about creating an ornithological group which would include stakeholders such as the Royal Society for the Protection of Birds (RSPB), who would review the monitoring that is to take place for the EMMP, and advise the decision maker that it would be acceptable to progress to a larger phase due to a better understanding of the collision risk or lack of it. This statement does not appear to take account of this; perhaps it should read “regulators, having consulted the advisory groups” instead.
31. Page 1, para. 7 states: “No device operation will be allowed until Regulators are satisfied that effective monitoring is in place that can directly inform the implementation of the EMMP, and inform the agreed aims, objectives and management questions set by the EMMP for the Project. Such requirements are expected to include the ability to detect marine mammal movements in proximity to deployed devices, to differentiate between marine mammal groups (for examples seals and cetaceans), and to detect or infer that collisions have (or may have) occurred.” Again, this should also be the case for marine ornithology, and this only mentions regulators and not the advisory groups, which should include the RSPB. Perhaps it should read “regulators, having consulted the advisory groups” instead. | The Applicant maintains that the paragraph is clear that the Regulators must be satisfied that effective monitoring is in place that can directly inform the implementation of the EMMP aims, objectives and management questions. This is intended to be a brief introductory section and the full details are provided throughout the document.
32. Page 5; para. 27 states: “The Applicant is committed to working with Regulators and RSPB to develop an agreed DEMMP [Detailed EMMP] post consent and proposes following an adaptive management approach during the implementation of that DEMMP.” This would benefit from being placed in paragraph 6, page 1 and perhaps should also include “pre-consent” in terms of the appointment of the group. | As discussed above, the Applicant maintains that the drafting is sufficiently clear.
33. Page 5; para. 29 states: “The implementation of mitigation, monitoring and management measures will be agreed with regulators and overseen by an independent Advisory Group.” Clarification is required over whether there would be topic-specific “advisory groups” or just one overall group. | It is the intention to have one Advisory Group overseeing the EMMP. Note that in the revised version of the outline EMMP (Document reference MOR/RHDHV/DOC/0072 (09)), also provided to NRW Licensing by email 15/2/21) the referenced text is now found within Section 1.3.1, para 38.
34. Page 6, para. 30; Phase 2 states: “If the results of monitoring of the first phase of deployment indicate that the next phase of deployment could begin without an adverse effect on marine mammals or birds, then the next phase of deployment would be authorised for deployment. An example of a commercial level of deployment for a second phase of deployment is suggested in the ES, Chapter 25, Socio-economics, Tourism and Recreation, as 40 MW;” However, the level of this next phase of development and the timing would depend on the adequacy of the results from the monitoring. This would be the same for all phases of development. | This paragraphs starts with "Indicative examples of potential phases of deployment are outlined below", with the preceding paragraph stating "Build out to the Project’s maximum installed capacity will be through a series of phases, with the number and scale of each phase of deployment linked to the outcomes of the EMMP". Therefore the Applicant maintains that it is clear that the phase 2 described is an example and agrees with NRW that each phase would depend on the results from the monitoring.
35. Page 11; para. 2.3.1: Pre-consent states that: “An Advisory Group and Independent Chair will be agreed by the Applicant and the Regulator”. We would advise that the RSPB should be invited to assist with these appointments, especially as pre-consent this group will “agree the aims and objectives, of the EMMP and Terms of Reference for Regulators’ approval.” Also “The Advisory Group will review monitoring questions for and agree appropriate methods of monitoring”. Page 5, para. 27 states that: “The Applicant is committed to working with Regulators and RSPB to develop an agreed DEMMP post consent and proposes following an adaptive management approach during the implementation of that DEMMP.” In order for the RSPB to help and agree with monitoring and mitigation we advise that they are involved at the pre-consent stage; post-consent is likely to be too late as the oEMMP states that this will be agreed pre-consent. | The Applicant maintains that appointment of the Advisory Group should be by the Applicant and Regulator and that RSPB will be invited to join the Advisory Group. The Applicant agrees that the Advisory Group will be able to contribute to the aims and objectives of the EMMP and Terms of Reference, as well as the monitoring questions and methods once the Advisory Group has been established.
36. Page 12; para. 67 states: “At each quarterly review the Advisory Group will consider: Whether the monitoring works being undertaken are generating data that can answer the EMMP monitoring questions agreed by the Advisory Group (see Section 2.6); and If any data collected suggest that a change in the current tier of applied mitigation should be considered. If the answer to either question is positive, then the Advisory Group will advise the Regulator as to the changes required and the Regulator will instruct the Applicant appropriately.” It should be noted that many years of data will likely need to be collected about the different devices for the Advisory Group to be content with the results. | Noted
37. Page 14; Plate 2-1; Illustration of EMMP process for initial deployment and repowering “Gate review 1. Year 1 - AG and regulator review of significance of EMMP outputs”. The oEMMP states that evidence will be collected on avoidance as well as significant impacts. The duration of the first phase deployment would be dependent on the efficacy and accuracy of the monitoring. Regarding the text box that states, “mitigation deployed and tested”, clarification is required as to what this mitigation refers to, or whether this is just for the first phase. If mitigation is implemented at the outset of the first phase, we are uncertain how it would be possible to learn anything about avoidance and collision rates. | The mitigation referred to is likely to be acoustic deterrent devices. These would be deployed and tested to confirm that it is operating correctly to provide confidence prior to the Phase 1 deployment.
38. Page 16; Table 2-1, Outline Monitoring Indicators; I1 & I2: With regards to “change in use of tidal device array deployment area pre and post installation”, clarification is required about whether the applicant is planning on using the original baseline boat surveys or new vantage point type surveys to inform this. To obtain a sufficient baseline we would expect there would need to be at least 2 years’ worth of data to compare with post-construction. Post-construction boat-based surveys may be impossible in the deployment area due to devices stopping transit on account of the potential collision of boats. | This is a decision for the Advisory Group during the development of the detailed EMMP. Agreement and finalisation of appropriate monitoring indicators will be a task for the Advisory Group during the development of the detailed EMMP. In undertaking this task, the Advisory Group will consider the type of technology to be deployed and the location within the MDZ of that deployment. The Advisory Group would make use of all relevant data to inform decisions, and this may include existing EIA baseline data, as well as the collection of new baseline monitoring data. Regarding the ability, or non-ability to collect data / undertake surveys, this decision is for the Advisory Group in their review of appropriate monitoring methods for each phase of deployment and for the project overall.
39. Page 16; Footnote 1 states: “Deterrent devices could include acoustic deterrent devices (ADDs) for marine mammals or visual deterrents for diving birds.” It has been shown (Melvin et al., 2001) that ADDs can reduce bycatch of guillemots in set nets and therefore could potentially be used as deterrents for guillemots in this case, provided they do not adversely affect SAC features or European Protected Species. | Potential to use ADD for diving birds has been included in the OEMMP and this footnote amended.
40. Page 17; Outline Monitoring Indicators; I7 mentions considering “local population effects, changes to local colony numbers over time, potentially indicating changes to mortality or breeding success” for diving birds. However, this would take a considerable number of years to enable changes potentially to be detected and therefore could not be achieved in the single year that is mentioned in Plate 2-1. | Agreement and finalisation of appropriate monitoring indicators will be a task for the Advisory Group during the development of the detailed EMMP. It is anticipated that some of the monitoring indicators and associated monitoring questions may have longer associated timeframes than others. Plate 2-1 of the outline EMMP (Document reference MOR/RHDHV/DOC/0072 (09)) shows an outline process envisaged for the EMMP, and for simplicity a yearly cycle of reporting is presented.
41. Page 23; Table 4-1: the applicant mentions the use of Active Sonar but only in terms of marine mammals. Clarification is sought over whether this could also be used for marine birds to look for avoidance behaviour around tidal devices and potential collision with tidal devices. We consider that the scoping in or out of such techniques should be a role of the advisory group. | Table 4-1 now reflects that active sonar may be used for marine mammals, seabirds and migratory fish. Paragraph 149 of the OEMMP also confirms that "all the methods summarised and any new and developing technologies will be considered and reviewed during development of the EMMP"
42. Page 23; Table 4-1; Surface infra-red/visual spectrum cameras: Considering the use of the area pre- and post-construction would require a statistically adequate pre-construction baseline to obtain a robust idea of usage. | The appropriate use of monitoring methods and their application to monitoring questions and indicators will be a task for the Advisory Group during the development of the detailed EMMP. Review of the methods detailed in Table 4-1, agreement of appropriate monitoring and mitigation methods, as well as monitoring questions and indicators will be a task for the Advisory Group during the development of the detailed EMMP pre-deployment, taking account of technology and location for deployment. Baseline data requirements will form part of this judgement.
43. Page 24; Table 4-1; Underwater Camera: Again, this is noted as a potential technique which would require data about the change in use of the tidal device area pre- and post-construction. This would also require a statistically accurate technique lasting an adequate amount of time. | As noted for response 42, above.
44. Page 23; Table 4-1; Acoustic Deterrent Devices: As mentioned earlier, these have been proven to work for guillemots as well as marine mammals. | Consideration of ADDs for birds has been added
45. Page 30-31; 6.2. Diving Seabirds; para. 135: As evidence of collision and avoidance behaviour is to be collected for marine mammals, it should also be collected for diving seabirds. | The Applicant maintains that para 135 is appropriate and that it may be suitable to monitor behaviour/habitat use at coarser scales (e.g. development area) and provide evidence/data that inform collision estimates. This could be via adequate refinement of the collision models and/or some level of monitoring of collisions/near-field interactions at devices, as well as in the medium to long term via monitoring of numbers and breeding productivity at the colonies. It is also noted that NRW in their closing to the Inquiry (available at: https://www.dropbox.com/s/ss3831dg1rszuqg/Morlais%20Closing%20-%20NRW.pdf?dl=0) stated "NRW does not expect the potential impact on birds to be monitored in exactly the same way as the impact on marine mammals. Rather, the extent of monitoring should be appropriate (and proportionate) to the extent of protection afforded by law and policy. NRW would expect the extent of the required monitoring (for all species) to be agreed by the Advisory Group identified in the oEMMP"
46. Page 31; para. 136 states: “Non-use of the array area by species being monitored during the first phase of deployment would be expected to lead to agreement that any pathway for effect on those species through collision did not exist.” We do not believe that the conclusions of monitoring should be pre-empted, and this would only relate to the devices deployed in Phase 1; the species may be present in other areas to which the project expands. | The applicant agrees that it is not appropriate to pre-judge the work of the Advisory Group in development of the detailed EMMP. This was not the intention of the text quoted. Without pre-empting any monitoring outcomes, it is reasonable to expect that if data collected pre and post deployment shows non-use of the deployment area by seabird species which are the subject of monitoring, then the Advisory Group and Regulators may agree that a pathway for collision at that location does not exist. This is not intended to pre-judge the outcome of any monitoring or review work undertaken by the Advisory Group, but to note a general principle that the presence of a source, pathway and receptor for an impact at a location, is required to determine that the potential for an impact exists.
6.0 Marine Mammals
ES Volume I, Chapter 12
47. Our remaining comments following review of the additional information are summarised as follows: | See responses below
48. Further to our original response (our ref. CAS-104373-N8Z1, date: 10/01/20) we are not aware of any additional information showing a change to the species sensitivity in the Environmental Impact Assessment. The EIA methodology fails to incorporate the ‘location importance’ and ‘value’ judgements on species. Sensitivity categorisation is therefore questioned and results in the significance of impact being less than it should be in some cases. | As stated in section 12.4.4.2 of ES Chapter 12, all species of marine mammal have been considered to be high value and the value of each species is used, where relevant, to modify the sensitivity of each species. However, as outlined in Section 12.4.4.2, high value and high sensitivity are not necessarily linked. A receptor could be of high value but have a low or negligible physical/ecological sensitivity to an effect. Therefore, the species sensitivity has been taken into account in the assessments. This takes into account the individual receptors capacity to avoid the anticipated impact. In addition, an assessment of each marine mammal species has been completed based on the sensitivity value of each population within Welsh waters, as defined by Sparling et al. (2015), for context and comparison only, for the assessment of collision risk. The summary of the potential impacts on marine mammals in ES Table 12-108 takes into account the value and sensitivity combined. For collision risk with operation turbines this has been assessed as high for bottlenose dolphin and low for all other species, including harbour porpoise. However, if the value and sensitivity combined is assessed as high for harbour porpoise the overall residual impact could change from minor to moderate adverse. However, this does not take account of the mitigation secured through the EMMP which will ensure there will be no adverse effect on marine mammals from SACs. This has been agreed by NRW as stated in their closing to the inquiry: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect."
Outline Environmental Monitoring and Mitigation Plan (oEMMP) (MOR/RHDHV/DOC/0072 (03), F5.0, 03/07/20)
49. We welcome the addition of the following statement in paragraph 7 of the revised oEMMP: “No device operation will be allowed until Regulators are satisfied that effective monitoring is in place that can directly inform the implementation of the EMMP, and inform the agreed aims, objectives and management questions set by the EMMP for the Project. Such requirements are expected to include the ability to detect marine mammal movements in proximity to deployed devices, to differentiate between marine mammal groups (for examples seals and cetaceans), and to detect or infer that collisions have (or may have) occurred”. | Noted
50. The oEMMP makes several references to updating the collision risk models using operational data, thereby reducing the predicted significance of collision impacts e.g. para. 19. The EMMP will collect data to update the models, with the expected output of reducing the predicted significance of operational collision effects. Therefore, we advise that the HRA process should address the project in its entirety prior to consent being given, and consider the predicted impacts as presented, as we do not consider it appropriate to revise the HRA post-consent. The applicant would need to demonstrate that the adaptive management would ensure the project reduces impact before AEOSI levels are reached. For example, where there is uncertainty over predicted collision risk with a high number of predicted collisions, the oEMMP would need to demonstrate mechanisms to prevent those collisions from occurring. If, as the EMMP suggests, new information then becomes available during the operation of the devices to show that the collision risk is lower than previously assumed, the risk of causing that AEOSI is reduced. | As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148] further progress has been made during the course of the Inquiry, including updates to the oEMMP and draft conditions. As concluded in NRW closing paragraph 37: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision-maker that there would be no such adverse effect."
51. The oEMMP details phased deployment of arrays of tidal devices (Section 1.3) giving indicative examples of potential phases of deployment e.g. para 30, as outlined below: | N/A
52. “Phase 1: Will be installed at a capacity (MW) at which no significant impact is predicted on marine mammals or diving birds using the MDZ. This commitment ensures an initial level of mitigation in place at the start of the EMMP through the limitation of the scale of the development”. The collision risk modelling for the proposed Phase 1 shows the potential for significant impact on harbour porpoise as well as being at the limit of significant impact for bottlenose dolphin. However, there is considerable uncertainty around the modelling (see paragraphs 81 – 89 below). We therefore advise that it is incorrect to state that the scale of Phase 1 represents sufficient mitigation to rule out AEOSI. | See response to row 139 above. In adddition, as stated in NRW's closing [Inquiry Doc - 148] paragraph 36(3): "NRW also notes and welcomes the Applicant’s confirmation in the final draft of the oEMMP that the EMMP (including its adaptive management provisions) will apply to all phases of the proposal, including the first phase: see para. 7."
53. “Phase 3: If the results of monitoring of the second phase of deployment indicate that the next phase of deployment could begin without an adverse effect on marine mammals or birds, and then the next phase of deployment would be authorised for deployment. If the monitoring and mitigation requirements are still required these would continue. Note it is the Applicant’s intention to remove monitoring and mitigation requirements as soon as it is possible to do so”. We do not agree with the stated intention to remove monitoring and mitigation requirements. It is likely that monitoring will be required throughout the project operation as it will be necessary to monitor animal movements in and around the array to detect any collisions that might occur. Mitigation must be available to be deployed in the event of any collisions to reduce the risk of further collisions reaching adverse levels. | The Applicant maintains that the removal of monitoring and mitigation requirements may be appropriate. The monitoring and mitigation methods will be reviewed and assessed throughout the deployment and different Phases, to ensure the most adequate, effective and suitable methods are in place at each stage. This may include the removal, adaptation or introduction of different methods based on lessons learned from previous phase(s) and any new techniques. The commitments of the EMMP will be met for all stages of the project, however, how this is achieved is likely to change and develop as the project develops. As discussed during the Inquiry EMMP session, the wording of the OEMMP (para 40) has been changed to reflect that the Applicant will "propose to remove monitoring and mitigation requirements as soon as evidence gained from the EMMP shows that it is appropriate to do so". The OEMMP is clear that the removal of monitoring and mitigation would require agreement of Regulator.
54. Para. 39 states that a tiered hierarchy of mitigation will be developed. We support this, including the stopping or removal of devices as a failsafe option. | Noted
55. Section 1.3.4 discusses ‘Trigger points’. We welcome the suggestion of using spatial trigger points for management actions. However, it is not clear whether these are intended to trigger action in real time to prevent possible collisions, and if so, how this relates to implementation of the mitigation tiers. An animal could move through the various spatial trigger points from far-field to near-field to the potential collision zone very rapidly as it swims towards a device. The oEMMP therefore requires further detail on how these trigger points will be implemented to reduce predicted impacts. | As outlined in the NRW closing [Inquiry Doc - 148] paragraph 38: "Insofar as NRW would have preferred the oEMMP to contain further detail on certain aspects, it accepts that these matters can be progressed further if and when the detailed EMMP is discussed in due course." This will include further discussions, details and agreements with regards to real-time trigger points, monitoring and mitigation methods.
56. Para. 55 states: “Updated modelling is expected to show that avoidance of operational tidal devices is much higher than assessed within the ES and that the level of deployment (MW) for which no significant effect is predicted for both marine mammals and seabirds can be revised upwards, allowing further phases of tidal device deployment”. There is no evidence presented to support this expectation of higher avoidance of operational tidal devices. Please note our previous comments relating to the need for the HRA to assess the entire project as presented. | The collision risk modelling was used to determine the maximum number of devices and MW output to provide the ‘Rochdale Envelope’ for Phase 1 of the Morlais Project by establishing the maximum limit and therefore any deployment would be less than those assessed. As each of the device type parameters used in the assessments are indicative to cover a range of possible turbine types in each category of tidal turbine design (as outlined in Table 4-2 in Chapter 4 of the ES) and the final design is still to be determined, results are shown as an example for a number of these devices, and for the maximum MW possible for each of the device types. These assessments are based on realistic worst- case parameters for tidal devices and linear scaling of individual devices to array, assuming all devices in array could have the same collision risk. The assessments also assume, as a worst-case, that all encounters and collisions are fatal. The assessments, although based on 98% avoidance rate, do not take into account mitigation and monitoring. Development of detailed EMMP will involve updated collision risk assessments prior to deployment, based on the latest information and tidal device parameters. This is likely to refine the modelling results as the tidal device parameters will be actual parameters for the tidal devices to be deployed rather than worst-case parameters for the device type categories that have been currently modelled as a worst-case. As discussed above, an AEOSI can be ruled out at this stage due to the commitments in the OEMMP and secured through the proposed ML condition.
57. Para’s. 66 - 68 discuss the review of monitoring measures by the Advisory Group e.g. through quarterly review, or at Gate Reviews to review the results to date; this may include options to deploy deterrent measures to mitigate any identified potential for collisions. We agree that this is appropriate for the broader monitoring questions, but not sufficient to deal with the risk (in real time) of animals colliding with the devices and an adverse effect occurring. The mortality limits for some marine mammal species are so low that a rapid response will be required even if a single collision is detected, in order to prevent further collisions causing adverse effect. The process described in these sections does not appear to allow such a rapid response. | Outside of the Gate Review process, the mechanism for management of real time incidents or collisions is the proposed collision of incident management framework, outlined in Section 2-5.
58. Plate 2-1 (Illustration of EMMP process). The 'mitigation deployed and tested' text box should also include monitoring as it will be essential to be able to detect and monitor marine mammals as they move in and around the device arrays. Regarding the 'Mitigation effective?' text diamond we agree that the mitigation should be tested and in working order before deployment, but it may not be possible to ascertain that mitigation is effective in reducing marine mammal collisions until it is used in the field. It is important to acknowledge that the efficacy of the mitigation methods in reducing marine mammal collisions is untested. | The Applicant is committed to demonstrating monitoring is effective before operation of devices, as detailed in the oEMMP.
59. Plate 2-2 (Illustration of incident management process). The incident management process does not allow for real-time assessment of real-time monitoring data. It may be necessary to implement actions in rapid response to incidents. | An updated Plate, now plate 2-3, has been provided by NRW for inclusion within the outline EMMP (Document reference MOR/RHDHV/DOC/0072 (09)). The updated plate shows an outline process for incident management, which allows for real time monitoring. The outline EMMP also makes clear a commitment real time monitoring, in particular with reference to trigger points (para 70) and within Table 4-1 .
60. Table 2-2 (Outline Monitoring Questions). Several of the monitoring questions concern potential revision of the collision and encounter risk modelling. While we agree that this will be useful to monitor to improve our understanding of the effects, it will not be possible to revise the assessment of impact significance post-consent as the assessment will be made against the entire project, pre-consent (see paragraph 50 above). A review of the collision and encounter risk modelling may however inform the scale of subsequent phases, which will be required to fall below the level of adverse effect. | Please note the earlier response to Paragraph 50. The outline EMMP is intended to inform the scale of all phases of deployment in a way that ensures no significant adverse impact on species groups monitored.
61. Section 4 (Outline Approach to Mitigation and Monitoring Methods). We note that the Marine Mammals Monitoring and Mitigation Options document (MOR/RHDHV/DOC/0119, F1.0, 25/03/20) provides more detail on the proposed methods. We suggest that this is included within the oEMMP to allow confidence that it will be effective in removing predicted adverse effects. This section considers several routes to mitigation including the slowing or other modification of the operation of installed tidal devices to reduce the predicted risk of collision. We support the consideration of this option as mitigation, however there is no information on how this might work. We would welcome further discussion on how device or operational modification could potentially mitigate collisions. We require clarification on how these two documents relate to each other. | As noted, a range of possible monitoring and mitigation options were provided in the note on Marine Mammals Monitoring and Mitigation Options. Some of these have been include as possible examples in the OEMMP. However, all possible monitoring and mitigation options will be reviewed and assessed for consideration in developing the detailed EMMP, including new and emerging technologies, as the detailed EMMP is developed and more information is available on effectiveness and any limitations of the potential monitoring and mitigation options, as well as details of the tidal devices, array layout and the mitigation and monitoring requirements.
62. We also suggest the applicant considers using operational monitoring information on the movements of animals to inform any modification of operation as mitigation. For example, if the monitoring data show that animals are more likely to be active in the area at a particular tidal state, modifications could be made to reduce operation during those more sensitive times. This section also considers mitigation through the temporary or permanent stopping or removal of deployed tidal devices. We welcome the inclusion of this in the oEMMP, which would give confidence that a failsafe option is available to avoid adverse effect through collision, should all other mitigation fail. | The suggestion is noted regarding operating approaches responding to actual data regarding real use of the site by potential receptors, and will be considered by the Advisory Group during the development of the detailed EMMP.
63. Section 119 of the oEMMP states that: “All of the monitoring methods proposed for consideration are described in monitoring literature, and their use is considered to be realistic, effective, sufficient and deliverable, with their use depending upon the monitoring question to which they are addressed”. We do not agree with this statement as there are considerable uncertainties on how the monitoring will be implemented, and whether it will be effective. Further detail on this is provided below. | This comment is noted, however, we disagree. Under the process in the outline EMMP (Document reference MOR/RHDHV/DOC/0072 (09)) monitoring and mitigation options will be reviewed and assessed for inclusion in the detailed EMMP. No monitoring or mitigation options within Table 4-1 of the outline EMMP have been discounted at this stage. NRW Advisory has noted in its closing submission to the TWAO Inquiry (provided to NRW Licensing by email 15/2/21), para 36 (4) that “NRW further welcomes the Applicant’s confirmation in the oEMMP that it will retain an open mind when considering monitoring and mitigation technologies (para. 149) and that the text suggesting the contrary in a previous draft of the oEMMP (in particular, in relation to Table 4.1) has been removed.”
64. Table 4-1 is titled ‘Review of Potential Monitoring Methods’, but also includes mitigation methods in the form of acoustic and visual deterrents. Our comments on each of the suggested monitoring methods are as follows: | Table 4-1 has been amended to clarify that it includes monitoring and mitigation.
• Passive Acoustic Monitoring (PAM): we agree that PAM will be crucial in monitoring marine mammals around the project both for long-term impact monitoring and real-time monitoring of the operational devices. While PAM has been demonstrated to be effective in locating vocalising marine mammals when used on seabed-mounted devices, it is unclear whether it can be effective within floating arrays. There are technical challenges in using a hydrophone array to locate animals in strong tidal currents. PAM is ineffective in monitoring non-vocalising animals such as seals, and potentially minke whales and other baleen whales which do not vocalise as frequently as toothed whales (i.e. dolphins and porpoises). | A range of possible monitoring and mitigation options were provided in the note on Marine Mammals Monitoring and Mitigation Options (MDZ_A28.13 MMC142 MOR-RHDHV-DOC-0119). Some of these have been include as possible examples in the OEMMP. However, all possible monitoring and mitigation options will be reviewed and assessed for consideration in developing the detailed EMMP, including new and emerging technologies, as the detailed EMMP is developed and more information is available on effectiveness and any limitations of the potential monitoring and mitigation options, as well as details of the tidal devices, array layout and the mitigation and monitoring requirements.
• Active sonar: we agree that this could be useful to detect animals close to devices, however these systems are still in the early stage of development. At present it is not clear how active sonar would be used to trigger ADDs. To date, the active sonar systems that have been trialled for use on operational tidal devices have been seabed-mounted; it is not clear whether this system could work for mid-water or surface-mounted devices. The use of active sonar is limited to close range detections and would be unlikely to be effective for wider field monitoring.
• Acoustic Deterrent Devices: we consider the use of ADDs to be a form of mitigation, not monitoring, and therefore this technique should not be included in this table. If this table is intended to discuss mitigation as well as monitoring, the other forms of mitigation previously listed in Section 4.1 should also be included. ADDs can potentially be used to deter animals from coming into danger of collision with the devices, but although this is theoretically feasible, their use for tidal energy devices is yet unproven. There is limited evidence of the efficacy of ADDs for certain species including bottlenose dolphin. While they may react in similar ways to other species, a precautionary approach should be applied as it cannot be assumed that they would be effective. ADDs introduce additional noise to the environment and are designed to disturb marine mammals causing them to flee from an area of danger. We are concerned about the potential disturbance caused by long-term use of ADDs. The purpose of the ADD should be to deter animals from immediate danger at close range, rather than cause them to flee large distances, as is the case when using them to mitigate injury from piling for example. We would advocate using an ADD with the lowest source level possible; enough to elicit a short-range avoidance of immediate danger of collision, whilst minimising wider disturbance impacts. Clarification is required on how ADDs would be configured in an array scenario, particularly how the applicant would ensure animals are not deterred from one device to flee in the direction of another. We support the aspiration to use an automated ‘detect and deploy’ system using active sonar to trigger ADDs, thereby limiting their use, but caution that such systems are, to our knowledge, still unproven in the field. | Table 4-1 has been amended to clarify that it includes monitoring and mitigation. The use of ADDs will be considered as the final EMMP is developed post consent, in consultation with NRW. It is important to note that, ADDs would only be activated if marine mammals were in close proximity and there is a potential risk of collision. The type(s) and number of ADDs to be deployed would be based on the latest technology and information to ensure adequate and effective mitigation. Activation of the ADDs and disturbance range of the ADDs would be determined to the lowest source level possible that would ensure the marine mammal is beyond the range of potential collision risk, but without causing any significant disturbance or increased collision risk with other devices. There is a commitment in the oEMMP that the underwater noise from ADDs will be reviewed as part of the ongoing development of the EMMP to ensure there is no significant disturbance or adverse effects. There is also a commitment in the oEMMP that the mitigation methods will be proven to be effective prior to any tidal device operation.
• Underwater cameras: we note that this technique has been discounted from further consideration in the oEMMP as it is "dependent on good visibility which is not always present at MDZ". We suggest that this technique should be investigated further considering recent successes at other tidal development sites. We query whether an assessment of the visibility at the project site has been made on which to base this assumption, and if so whether this information should be submitted as evidence to the decision maker. If cameras are not used it might not be possible to determine what has collided with the device, thus a ‘worst case scenario’ must be assumed, i.e. that the collision was with the species with the lowest collision limit. | The OEMMP has been amended to clarify that no monitoring options have been discounted, including underwater cameras.
65. Our comments on the additional proposed methods are as follows: | All possible monitoring and mitigation options will be reviewed and assessed for consideration in developing the detailed EMMP, as the detailed EMMP is developed. No monitoring or mitigation options have been discounted at this stage.
• Seal Tagging Studies: we welcome consideration of seal tagging to better understand potential impacts on seals. However, as this monitoring method is not included in the oEMMP, we request clarification on whether it is being considered further.
• Light Mitigation methods, Thermal Imaging Technology and Underwater Cameras: these mitigation methods are listed as options in the Marine Mammals Monitoring and Mitigation Options document (MOR/RHDHV/DOC/0119, F1.0, 25/03/20) but discounted in the oEMMP. Note our previous comments above on the underwater camera monitoring method.
66. Section 6. Summary of outline of approach. We agree with para. 132 that the absence of evidence of collision and/or evidence of avoidance of the array or of devices within the array would be expected to lead to agreement that a further phase can be deployed. However, we do not agree with para. 136, which states that “non-use of the array area by species being monitored during the first phase of deployment would be expected to lead to agreement that any pathway for effect on those species through collision did not exist”. The absence of evidence of species in proximity to the array does not necessarily rule out the risk of future collisions. The risk may be different for each device type, and a larger array carries different risks than a smaller phase. | Please see response to paragraph 46.
Underwater Noise Modelling Report (MOR/RHDHV/DOC/0116, F1.0, 25/03/20) and Marine Mammals Underwater Noise Modelling Note (MOR/RHDHV/DOC/0117, F1.0, 25/03/20)
Construction drilling noise | Acknowledged
67. Based on the presented noise modelling, we agree that the potential noise injury impact from percussive drilling is likely to be minimal. The more conservative disturbance threshold estimates that drilling noise could potentially disturb animals to 6.9km. Although construction noise will be temporary, the ES suggests a worst-case scenario of up to 5.5 years of disturbance from drilling over a 10-year construction period. However, the disturbance radius and corresponding area of potential disturbance at this conservative maximum estimate falls below the limit of 20% over a day, or 10% over a season, of the area of North Anglesey Marine SAC so we agree that there would be no likely adverse effect from this activity.
Operational turbine noise | Further information was provided in the Marine Mammals Proof of Evidence Rebuttal [RPE004] and PoE [MDZ/P2]. As outlined in the NRW closing [Inquiry Doc - 148] in relation to underwater noise, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
68. This was modelled using estimated source levels for two models of tidal turbine: a small turbine with a rotor diameter of 16.13m and a larger turbine consisting of two rotors, each 24.6m in diameter with the source level scaled based on the rotor diameter of the proposed tidal turbine:
• 16.13m diameter rotor tidal turbine (small): 155.7dB re 1μPa @ 1m (SPLRMS1)
• Dual 24.6m diameter rotor tidal turbine (large): 161.2dB re 1μPa @ 1m (SPLRMS).
69. Clarification is sought on where these operational noise levels were sourced from, and whether it is realistic to assume that noise from the large rotor device will scale from the small rotor device. We also query whether these two source levels adequately consider the multiple different device types with potentially different noise characteristics. It is therefore not currently possible to assess whether the information presented is a realistic worst case.
70. The applicant maintains that a 142dB threshold taken from Hastie et al. (2018) is the most specific and relevant disturbance threshold available for this type of assessment, as the low-end threshold of 120dB (SPLRMS) for continuous noise disturbance for marine mammals from Southall et al. (2007) is approaching the level of background noise in some areas (Nedwell et al. 2003, 2007). However, rather than comparing against background noise published from other areas, we advise that the predicted noise level should be compared against that measured at the site by SEACAMS as reported in Table 1.1 of the Marine Mammals Underwater Noise Modelling Note (MOR/RHDHV/DOC/0117, F1.0, 25/03/20); maximum background noise was 106.6dB SPLRMS, while the average was 98dB SPLRMS. The lower disturbance threshold of 120dB is therefore higher than the maximum background noise measured at the site so could feasibly be audible to marine mammals.
71. Furthermore, the 142dB threshold is taken from Hastie et al. (2018), where playback experiments were conducted in the vicinity of harbour seals. The paper’s author has confirmed that 142dB does not really represent a threshold for avoidance, simply that these were the estimated levels within an area where seals showed a significant reduction in abundance, and that caution should be applied if using this as a threshold for other species (G. Hastie, pers. comm., 29/4/2020).
72. The validity of using a 142dB threshold for disturbance is further questioned when compared with the impact ranges from the Southall et al. (2019) weighted SELcum2 injury criteria. For example, the temporary threshold shift (TTS) range in Very High-Frequency cetaceans (including harbour porpoise) for a single large turbine is estimated to be a maximum of 230m, while the disturbance range is estimated to a maximum of 70m. This is evident in Table 1-21 of the Marine Mammals Underwater Noise Modelling Note (MOR/RHDHV/DOC/0117, F1.0, 25/03/20), which shows the maximum predicted TTS ranges for Very High-Frequency cetaceans (including harbour porpoise) alongside the maximum predicted disturbance ranges, with TTS ranges exceeding disturbance range for operational single turbines and ADDs. We therefore do not consider it appropriate to assume that animals might experience TTS at a greater distance than they would be disturbed.
73. The noise propagation from a sample array of small turbines was modelled at 620 locations, and large turbines at 120 locations (Underwater Noise Modelling Report, MOR/RHDHV/DOC/0116, F1.0, 25/03/20). The results are shown as noise plots (Fig 4-10 & 4-11) but the associated data are not presented. No estimate is given of what the maximum noise disturbance range would be for an array of either small or large turbines. However, the plots appear to show a range of up to approximately 17km from the centre of the array for the 120dB noise threshold. The plot for the large turbine array (Figure 4-11) does not appear to show any locations where noise exceeds 135-140dB. This does not appear accurate, given that the plot is modelled on an array of 120 turbines with an estimated source level of 161.2dB re 1μPa @ 1m (SPLRMS). The plot of the single large turbine (Figure 4-7) and the small turbine array (Figure 4-10) appear to show higher source levels than the large turbine array. Furthermore, the noise plot in Fig 4-11 does not appear to match the array configuration in Plot C of Figure 3-1. Clarification is therefore required as to whether this is accurate.
74. We seek clarification as to how the modelled arrays (of 620 ‘small turbines’ and 120 ‘large turbines’) relate to the proposed full project deployment. While 620 is stated for the worst-case scenario of the full deployment in ES Volume I, Chapter 4: Project Description (MOR/RHDHV/DOC/0004, F4.0, October 2019) it is not clear where 120 large turbines are derived from.
75. Given the lack of information on the range of potential disturbance impact, and the uncertainty over the accuracy of the information presented, it is not currently possible to assess the likely impact footprint of disturbance from operational noise, which will occur for the duration of the project. We therefore cannot agree with the conclusion of the report regarding operational noise and further information is required.
Acoustic Deterrent Devices (ADDs) | As outlined in the NRW closing [Inquiry Doc - 148] in relation to underwater noise, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
76. The Underwater Noise Modelling Report (MOR/RHDHV/DOC/0116, F1.0, 25/03/20) estimates a disturbance range of 840m based on the assumed disturbance threshold of 142dB (SPLRMS) from Hastie et al. (2018). This received noise level and associated avoidance by harbour seals should not be applied out of context as a disturbance threshold to all species from ADD use. The noise modelling further supports this, as it predicts temporary threshold shift (TTS) to harbour porpoise to a maximum range of 5.3km (Table 4-11, Underwater Noise Modelling Report, MOR/RHDHV/DOC/0116, F1.0, 25/03/20) based on the non-impulsive Southall et al. (2019) criteria for cumulative exposure (SELcum). Therefore, we consider it incorrect to assume that animals may only be disturbed to a range of 840m when they may experience TTS at far greater range.
77. The report also cites evidence from field trials and a review of the evidence base for application of ADDs as marine mammal mitigation (Brandt et al., 2012, 2013; McGarry et al., 2018) in which the disturbance range for the Lofitech ADD was estimated as 7.5km for harbour porpoise. This is cited as a worst-case in the ES for the potential displacement of harbour porpoise during ADD activation and we agree that this is the best available evidence for the effectiveness of this ADD. It is not appropriate to use assumed disturbance ranges based on 142dB for the reasons cited above, nor to use these assumed ranges contrary to peer-reviewed evidence supporting considerably larger disturbance ranges (Brandt et al., 2012, 2013; McGarry et al., 2020).
78. There is no information available on the effectiveness of the preferred Lofitech ADD on dolphin species, and very limited information for other devices. The assumption that a deterrence range for bottlenose dolphin from an ADD could be ‘more than 4km’ does not appear to be supported by evidence. The cited literature used to support this assumption (McGarry et al., 2017) is from a field trial on the effectiveness of ADDs on minke whales but there is no implication that the same is true in relation to bottlenose dolphin or any other species.
79. There is no information on how the ADD array will be configured and used, which ADDs would be used, how this might affect noise propagation, how ADDs might be triggered in response to marine mammals, or how disturbance from up to 40 ADDs would extrapolate across the array. We also request clarification on if/how the ADDs will interact with each other e.g. how the sound from one set of ADDs might interact with another set.
80. Given the uncertainty over the accuracy of the information presented and the lack of information on the likely deployment and configuration of the ADD array, it is currently not possible to assess the likely impacts from ADDs.
Marine Mammals Additional Collision Risk Modelling (MOR/RHDHV/DOC/0118, F1.0, 25/03/20)
81. Indicative scenarios are presented for the maximum number of each type of device combined in an array where the predicted collision risk is <0.7 bottlenose dolphin in line with the Potential Biological Removal (PBR) figure for this species. The collision risk was calculated through both collision risk modelling (CRM) and encounter rate modelling (ERM) to present the maximum number of devices and MW for each device type that would fall below 0.7 bottlenose dolphin collisions (assuming a 98% avoidance rate). | As outlined in the NRW closing [Inquiry Doc - 148]: further progress has been made during the course of the Inquiry, including updates to the oEMMP and draft conditions. As concluded in NRW closing paragraph 37: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision-maker that there would be no such adverse effect."
82. While the use of quantitative CRM or ERM models can be useful to indicate the general order of magnitude of the potential for collision and to compare relative predictions between different scenarios, it is inappropriate for a project of this scale to base the entire assessment on the quantitative outputs associated with such uncertainty.
83. Table 5-15 summarises the first phase collision risk for all species at a range of avoidance rates. Previous work (e.g. Band et al. 2016) has indicated that collision risk predictions are most sensitive to assumptions about the avoidance rate. There is no empirical support for the adoption of a 98% avoidance rate for this project. The collision risk for the first phase scenario ranges from 0.35-35 bottlenose dolphin; 1-1,245 harbour porpoise; and 1-197 grey seals per year. Given the clear sensitivity of the modelling to avoidance rate, with a wide range of outputs, the adoption of the 98% value cannot be considered ‘precautionary’ or ‘worst case’.
84. There is uncertainty on how collision rates will scale with multiple devices. The applicant uses a simple linear increase in collision risk with additional devices or MW to estimate different array scenarios. This is presented as a worst-case scenario. However, the applicant has not submitted evidence to support this and neither are we aware of any evidence on which to base this assumption. We currently have no information about how animals might behave around arrays and therefore this assumption is highly uncertain.
85. The first phase scenarios presented are at the maximum level of sustainable mortality of bottlenose dolphin based on a 98% avoidance rate. Considering the uncertainty, the concept of basing the first phase on a predicted collision estimate of 0.7 bottlenose dolphin is inappropriate. There is still a credible risk that PBR would be exceeded (causing AEOSI).
86. We note that the CRM and ERM outputs for harbour porpoise from the indicative first phase scenarios also present a risk of causing AEOSI with a potential collision risk of up to 25 harbour porpoise per year at 98% avoidance rate.
87. Given that NRW PS must carry out the HRA for the project for the whole application, the CRM and ERM outputs for the 240MW scenario must be considered. Noting the uncertainties, particularly around scaling and avoidance rate, the number of collisions presented in the assessments (Tables 4-1 and 4-2) are unacceptably high and we would be unable to rule out adverse effect on site integrity and significant population level effects. For example, a maximum collision risk at 98% avoidance rate of each Annex II species would be:
• >18 Bottlenose dolphins representing >6% of the management unit population
• >400 harbour porpoise representing 0.6% of the management unit population where bycatch is already causing a potentially unsustainable level of anthropogenic mortality.
• >83 grey seals representing 1.4% of the population where bycatch is already causing a potentially unsustainable level of anthropogenic mortality.
An assessment of collision risk at other avoidance rates for the full deployment is not presented, but we expect the figures would be higher at lower avoidance rates.
88. No additional information about the potential for animals moving through the site and the potential consequences of stopping that movement or displacing animal movements elsewhere has been provided. The deployment of 240MW (620 devices) will cause a physical barrier; the assessment has utilised the development’s total footprint area and density of animals in that area to describe the barrier. However, we advise that an assessment of ‘barrier effects’ requires information on the movements of animals through an area, rather than an area and average measure of density.
89. Based on the indicative phase 1 assessments we cannot be satisfied that the PBR for bottlenose dolphin will not be exceeded. The assessment places an over-reliance on the outputs of the quantitative predictive collision risk modelling with very little appreciation of the uncertainties inherent in this approach. We consider that the applicant should reduce the scale of the first phase array to reduce the risk considerably.
7.0 Water and Flood Risk
ES Volume I, Chapter 17
90. We are generally satisfied that ES Volume I, Chapter 17 and specifically ES Volume III, Appendix 17.1, Flood Consequence Assessment provide a true reflection of the flood risks and demonstrate that these risks can be managed. | Noted
91. We can confirm that our previous concerns regarding residual flood risk during construction have now been addressed. We welcome this and have no further comments to make on this topic. | Noted
8.0 Onshore Ecology - Holy Island Coast SAC/SPA/SSSI
ES Volume I, Chapter 19
92. Our remaining comments following review of the additional information are summarised as follows. | See responses below
Holy Island Coast SPA | Noted
93. The Onshore Ornithology: Response to Comments on Chough document (MOR/RHDHV/DOC/0120, F2.0, 05/05/20) has sufficiently addressed all three functional linkage tests and confirmed that the Onshore Development Area represents a significant contribution to the requirements of breeding and wintering chough from Holy Island Coast SPA.
94. Following our subsequent discussions with the applicant to mitigate the impact of tests 1 and 3 we advised the breeding season date should be extended so that no works occur from 20 March to 31 July and that, in association with a 500m buffer, two recommended exclusion zones (Areas 1 and 2) are provided. The document confirms that the applicant will include additional mitigation to ensure no/negligible displacement of foraging breeding chough by providing two additional works exclusion zones for the defined chough breeding season (from 20 March to 31 July). These exclusion zones also cover the core foraging areas for breeding chough. We consider that the applicant has sufficiently addressed our concerns of functional linkage between the Onshore Development Areas and the Holy Island Coast SPA with this additional mitigation. | Noted
Holy Island Coast SAC (including Holy Island Coast SSSI)
PDE Matrix Spreadsheet (MOR-RHDHV-DOC-0127, F1.0, 22/05/20)
95. We welcome the changes made to the revised PDE matrix spreadsheet, making it more consistent with the other supporting documents. | Noted
96. Rows 29/30: the potential trenching across the foreshore and associated worst-case scenario loss of 31,700m² (0.7% of Holy Island Coast SAC/SPA/SSSI) should be expressed as a percentage of the habitat/SSSI feature, as well as the whole site, which is 3.1 hectares; the intertidal element of the SSSI is narrow and this appears to be a large extent for the trenching. We advise that these figures are checked as 3.1ha may well be the extent of trenching, but not all within the Holy Island Coast SSSI/SAC/SPA foreshore. If it is correct, this would be a significant impact resulting in a major loss of habitat within a European protected site. Furthermore, it is not clear how the trenches across the foreshore will be infilled and therefore whether there would be lasting impacts. Clarification is required on this. | The estimated habitat loss in the intertidal area is 7,400m2 (0.0074km2) as assessed in the ES. With the refined landfall cable route, the area of cable trenching in the intertidal zone is likely to be approximately 250m2 (25m between MHWS and MLWS x 10m trench width). The area of potential works in the intertidal zone does not interact with any of the notified habitats or species of the Glannau Ynys Gybi / Holy Island Coast SSSI/SAC. Glannau Ynys Gybi SSSI has other habitats/earth science features that contribute to the special interest, including rockpools, overhanging rock, gullies and under boulder communities and their associated flora and fauna. These are components of the special interest of the site and therefore will be avoided where possible, however there is not statutory mechanism by which they are protected within the SSSI.
97. Row 56, non-native invasive species. No worst-case scenario is presented with a justification that it is related to construction rather than operation. However, there are risks associated with an operational working footprint: seeds or other propagules may be brought on site during maintenance works or routine operations on any part of the system, including the J-tubes and the substation. Risks are low, but impacts could be significant if a new invasive species were introduced to the designated sites. | Row 56 states "No WCS paramters associated this impact as related to construction process rather than working footprint.". Section 19.6.5.14 of ES Chapter 19 Onshore Ecology provides the assessment of potential spread of non-native invasive species.
Cliff Habitat Survey report (MOR/BSG/DOC/0001, F1.0, 03/07/20) | Noted
98. Para. 4.49 states that Annex I habitat is present over much of the cliff and cannot be avoided if cables are pinned to the cliff. We agree that this is an adequate summary. The report suggests that micro-siting could minimise impacts, which the Cliff Habitat Design Refinement note expands upon (see next).
Cliff Habitat Design Refinement note (MOR-RHDHV-DOC-0135, F1.0, 03/07/20) | Noted. The visual impact of placing the J-Tubes on the cliff face is considered in Chapter 24 Seascape, Landscape and Visual Impact Assessment of the Environmental Statement (Document MMC077 MOR-RHDHV-DOC-0054). The Landscape Management Plan produced post-consent under Condition 7 of the draft planning conditions will include details on how landscape planning will mitigate visual effects of the J-Tube, whilst remaining in keeping with the ecological requirements of any planting in the vicinity of the SAC / SSSI. As outlined in Section 6.1.2 of the Terrestrial Ecology Assessment Update v04 (Document MMC189 MOR-RHDHV-DOC-0110 (4)) submitted in October 2020, the project Ecological Clerk of Works (ECoW) will be present during construction to advise on the micrositing of the J-Tube anchor points to avoid areas of vascular plant interest as identified within the Cliff Botanical Survey (Document MOR-BSG-DOC-0001).
Section 4, Micro-siting:
99. Although our preference would be for Horizontal Directional Drilling (HDD), if the cables had to be placed on the cliff, we would welcome the proposal to locate the J-tubes on bare rock as far as possible. However, the visual impact of this may need to be considered. Efforts to avoid Inula crithmoides and Limonium binervis, components of the vascular plant interest feature should also be made.
100. The assessment concludes that 0.023% of the designated SAC Annex 1 habitat feature will be affected, including the working zone at each side (equivalent to c. 0.025 hectare) and refers to this as a de minimis impact. Mitigation/compensation will be necessary, even for this small percentage impact. | An Outline habitat enhancement plan (Document MMC578 MOR-RHDHV-DOC-0169) has been agreed with NRW to provide an overall improvement of the habitats which support the Glannau Ynys Gybi / Holy Island Coast SAC / SSSI through the commitment to habitat enhancement measures in proximity to the SAC at Abraham’s Bosom.
101. If HDD is successful, we agree that impacts on the designated sites would be minimal, subject to adequate pollution control. However, if trenching and J-tubes are necessary, we cannot agree that the potential loss of 3.1ha of intertidal habitat and 0.023ha of vegetated seacliff can be considered to have no significant effect. Table 8.1 of the Terrestrial Ecology Assessment Update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) records minor adverse impacts but the loss of a strip of vegetation down the cliff together with intertidal areas is potentially damaging. Vegetated seacliffs are a scarce and fragile habitat and slow to recover from any disturbance. The intertidal habitats are a supporting feature of the other habitats and without them the whole site will be devalued. | Should HDD not be possible at landfall, the secondary option to trench the cables at the landfall and associated works at the cliffs results in a worst case impact of up to 510m2 of cliff. As discussed above, the trenching area in the intertidal zone would be approximately 250m2.
102. It is estimated that maintenance works would be required on the J-tubes every 5 years, but this is only an estimate and a worst-case scenario could require far more frequent maintenance, and disturbance to the cliff vegetation. Based on the location, it is possible that the J-tubes will be regularly impacted by storms. In view of the available evidence therefore, we do not believe that an adverse effect on site integrity of the Holy Island Coast SAC can be ruled out for the trenching/J-tubes option. | As outlined in the Terrestrial Ecology Assessment Update v04 (Document MMC189 MOR-RHDHV-DOC-0110 (4)), the J-Tubes design has been modified to include structures (such as handholds) are able to support maintenance activities (i.e. inspection and repainting) without touching the cliff. This change will remove direct effects of cliff vegetation arising from maintenance during operation of the project.
Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20)
103. Section 7.1.2: we welcome the commitment to manage Japanese knotweed and any other INNS identified during the project. This should include Oxalis articulata which was found during the cliff survey and will spread readily from small fragments of plant material. The proposed 10m fenced buffer around INNS will not always be possible if they are found within a working zone. In this case, control methods should be included in the INNS biosecurity risk assessment and management plan and undertaken before work starts. | Oxalis articulata is now specifically mentioned within the mitigation set out in Section 7.1.2 of the Terrestrial Ecology Assessment Update v04 (Document MMC189 MOR-RHDHV-DOC-0110 (4)). Reference to eradication prior to works is also included within Section 7.1.2, it would be part of the Invasive Species Management Plan, secured under Condition 3h pf the Draft Planning Conditions.
104. The updated proposals in the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) and Cliff Habitat Design Refinement note (MOR-RHDHV-DOC-0135, F1.0, 03/07/20) are a significant improvement on the original 90m wide working zone. The cliff vegetation survey carried out satisfactorily in May/June 2020 has shown that the proposed location for J-tubes supports high-quality vegetated cliff habitat. However, the worst-case cable-trenching scenario would still involve loss of SAC habitat (0.023% for J-tube width and working zones). Although a small percentage, we advise that the loss of any SAC habitat is significant, especially such a fragile and spatially restricted one. A recommendation has been made regarding micro-siting of J-tubes, but there will be other requirements to consider and we believe it is not possible to be certain that these recommendations can be followed and implemented. In view of this we regard 0.023% as the minimum amount of habitat that could be affected if J-tubes are installed. | Menter Môn’s position is that, following design refinement and micrositing, and with the mitigation set out in Sections 6 and 7 of the Terrestrial Ecology Assessment Update v04 (Document MMC189 MOR-RHDHV-DOC-0110 (4)) in place, installation of the J-Tubes represents a small-scale impact which is recoverable in the long-term, constituting an effect which is not significant in EIA terms or which constitutes an AEOI of the SAC (see Section 6 of the Terrestrial Ecology Assessment Update v04). Note that 0.046% is the maximum amount of habitat potentially affected - the micrositing is expected to give rise to effects upon 0.023% of the key areas of habitat, as approximately half of the cliff is bare rock, which does not support the key species which comprise the Annex I vegetated sea cliff habitat, however this cannot be confirmed exactly until detailed design, so 0.046% is the worst case.
105. No rare plant species were present within the proposed disturbance zone, but the habitats found are fully representative of this SAC feature. Therefore, we cannot agree with the assertion in Table 8.1 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) that impacts would be minor adverse and negligible. We consider that any loss of vegetated seacliff SAC habitat would be at least a moderate adverse impact.
106. The extent of Allium ampeloprasum alongside the road near SH217816 and the small-flowered catchfly Silene gallica should be identified through botanical survey. | ES Chapter 19 (Document MOR-RHDHV-DOC-0037), Section 19.6.5.13.1 sets out the mitigation for these species, which includes identification and demarcation of these species prior to construction. This would be undertaken through a botanical survey (this is now explicitly included in the drafting planning condition, see Condition 11h), and required mitigation included in the Ecological Action Plan (secured under Condition 3i of the draft planning conditions). In addition, NRW’s comment in the 9th October 2020 meeting that the Silene gallica may not be present every year and should be treated as potentially present within the EAP has been noted and Section 7.1 of the Terrestrial Ecology Assessment Update v04 (Document MMC189 MOR-RHDHV-DOC-0110 (4)) updated accordingly.
107. In order to install up to 100 rock bolts to secure the J-tubes, approximately 0.25m³ of rock would have to be drilled out. This could cause significant dust with the potential to smother plants downslope/downwind of the drilling site. The applicant states that dust extraction may be possible, but that this will depend on the contractor. We do not consider this an adequate approach; the vegetation survey showed that the cliff is well-vegetated across much of its surface i.e. supports a habitat for which the SAC is designated. This could be vulnerable to dust, and we advise that the methodology used for this work should be selected to minimise impacts on surrounding vegetation through dust or lubricants. | The approach to dust management is outlined in the Terrestrial Ecology Assessment Update (version F4.0, document MMC189 MOR-RHDHV-DOC-0110). This was agreed with NRW during the TWAO Inquiry process as shown in the Statement of Common Ground (document MDZ/L6)
108. Dust from general onshore construction works may also be a risk, but prevailing wind will likely take this away from the cliffs and it is more likely to impact heathland within the SAC. No consideration appears to have been given to this impact.
109. Impacts of dust have therefore not been adequately assessed due to a) an apparent lack of acceptance that drilling will cause significant dust and b) a lack of knowledge of what vegetation is present on the development route; therefore, we cannot be certain of the conclusion that impacts are likely to be low. In order to address this, we suggest that dust deposition outside the boundary of the works is subject to a condition that it must not exceed a specified level considered to be a nuisance in residential areas. This could be controlled via a dust management plan.
110. No mitigation or compensation has been proposed for impacts on the sea cliff vegetation, even though they are expected to be long term. There will be a loss of SAC habitat and, whilst direct replacement is not possible, compensation may be possible through restoration of some areas of improved or semi-improved grassland along the top of the cliff, which would enhance the coastal ecosystem allowing the development of a more natural transitional zone between vertical cliff and more level grassland/heathland. We would welcome engagement with the applicant in such discussions. | An Outline habitat enhancement plan (Document MMC578 MOR-RHDHV-DOC-0169) has been agreed with NRW to provide an overall improvement of the habitats which support the Glannau Ynys Gybi / Holy Island Coast SAC / SSSI through the commitment to habitat enhancement measures in proximity to the SAC at Abraham’s Bosom.
111. It is agreed that if HDD is successful, direct impacts on cliff vegetation will be avoided. There is however still a risk of indirect effects on both cliff and heathland vegetation through aerial deposition of dust and run-off of polluted water; these should be considered within the HRA. The Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) assumes that residual impacts of sediment-laden run-off affecting upper parts of the cliff would be negligible. However, the cliff survey found that the cliff was well-vegetated and as such it is vulnerable to eutrophication or smothering by silty run-off. A further risk is that of water flowing from a point source i.e. channelled through the working zone to a single discharge point and washing soil and vegetation from upper parts of the cliff. This should be prevented by a robust pollution prevention plan, but as there is a small risk of such measures failing there is a residual low risk of moderate impacts. | Mitigation measures proposed in Section 6 of the Terrestrial ecology Assesment Update (document MOR/RHDHV/DOC/0110) provide control measures for the sediment laden run-off to minimise the pathway of an impact. The measures proposed are intended to reduce the risk of pollutant release down to negligible levels, giving rise to impacts which are non - significant in EIA terms. The impact assessment was initially conducted assuming that sensitive plant species could potential be present within the cliff adjacent to the clifftop works, under a precautionary approach. Dust extraction equipment will be used during construction (see below), to minimise the risk of dust release during drilling works (See Section 5 of document reference MOR-RHDHV-DOC-0110). Although dust extraction measures will be in place, to further minimise the risk to sensitive habitats from residual dust generated by the works, a Dust Management Plan (DMP, see below) will be prepared which will include monitoring and control measures to be adhered to during construction . As described in version 04 of the Terrestrial Ecology Assessment Update (document reference MOR-RHDHV-DOC-0110), these will include: - Commitment to use drilling equipment fitted or in conjunction with suitable dust suppression techniques; - Details of dust monitoring - for works on the cliff on for dust generating activities within the wider project – undertaken during construction, and remedial measures employed should agreed thresholds be breached; - Restriction of weather conditions when dust generating activities on the cliff face are acceptable (i.e. during damp days). Full details of the measures which will be included in the DMP are provided in version 04 of the Terrestrial Ecology Assessment Update (document reference MOR-RHDHV-DOC-0110). Under Option 2 for cable installation at the cliff, the draw-pits are located within neutral grassland outside the SAC boundary. The Botanical Survey (Document MOR-BSG-DOC-0001) identified it as a species-rich grassland showing evidence of some limited improvement, and most closely associated with NVC community MG1 (Arrhenatherum elatius grassland). As a worst case, it has been classified as unimproved grassland for the purposes of this document. As outlined in Section 5.2.1 of the Terrestrial Ecology Assessment Update v04 (Document MOR-RHDHV-DOC-0110(4)), the ECoW will be present onsite to ensure the draw pits can be microsited into the least sensitive area.
112. Paragraph 210, Chapter 19 of ES Volume I (MOR/RHDHV/DOC/0100, F3.0, July 2019) concludes that HDD will result in no impact on the Holy Island Coast SAC/SPA/SSSI. However, it is unclear whether there will be large volumes of spoil generated: if so, measures will be needed to ensure no sediment-laden run-off flows down the cliff before concluding no impact is likely. Section 5 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) states that transition pits will be at least 220m back from the cliff. However, the proposed draw pits are still very close to the cliff edge. Although the Cliff Habitat Survey report (MOR/BSG/DOC/0001, F1.0, 03/07/20) shows quadrats within the unimproved grassland there are some inconsistencies in quadrat labelling between the map and the data tables, making it difficult to judge the impacts of the draw pits. The main risk associated with this work is loss of sediment and/or polluted water onto the cliff below.
113. The Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) states: “There are no marine (intertidal) notified features listed for the Glannau Ynys Gybi / Holy Island Coast SSSI. Glannau Ynys Gybi SSSI has other habitats/earth science features that contribute to the special interest, including rockpools, overhanging rock, gullies and under boulder communities and their associated flora and fauna. These are key components of the special interest of the site and therefore will be avoided where possible, however there is no statutory mechanism by which they are protected within the SSSI”. However, rock bags and concrete mattresses below the J-tubes would be expected to smother intertidal organisms. Although not a designated feature they are of local interest and an integral part of the designated site. Their loss through the project may be inconsistent with the biodiversity duty in section 6 of the Environment (Wales) Act so consideration should be given to minimising impacts in this area. | The Terrestrial Ecology Assessment has been revised and v04 (Document MOR-RHDHV-DOC-0110(4)) includes in Section 5.2.1 details of those features present within the intertidal zone. The landfall route has been refined to minimise the length within the intertidal zone, so that it now only covers approximately 30m of the zone between MHWS and MLWS. An Outline Biodiversity Enhancement plan (document MOR-RHDHV-DOC-0164) has been agreed with NRW. Section 7.2 describes habitat enhancement options in the intertidal zone.
114. Section 5.2.1 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) states that rock bolts would typically be made of high-yield steel or stainless steel, but at an increased cost. We advise that durability should be the overriding concern in order to avoid having to re-bolt the J-tubes during the life of the project in order to protect the cliff habitat from unnecessary maintenance works. | The methodology updated in the Terrestrial Ecology Assessment Update, Section 5 and assessment updated in Section 6 (document MOR-RHDHV-DOC-0110) to provide greater clarity. The rock bolts will be robustly designed accounting for the exposed environment. Both high yield and stainless steel are seen as providing a robust option for the rock bolts.
115. The Seascape, Landscape and Visual Impact Assessment Post-application Consultation Responses document (MOR/SLR/DOC/0001, F2.0, March 2020) refers to the use of planting to screen J-tubes where they rise 2m above the cliff edge. This may not be compatible with the vegetated sea cliff feature of the Holy Island Coast SAC, where low-growing grasses and dwarf shrubs such as heather or herbaceous plants would be more appropriate along the cliff top. Consideration must be given to local vegetation types to avoid introducing inappropriate species. See also paragraph 134 below. | Noted. The pre-construction vegetation survey will inform the development of the screening proposals to be included in the Landscape Management Plan. The Landscape Management Plan will be secured by condition of the TWAO and must be approved by the Planning Authority.
116. We welcome the commitment in the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) to restore “agreed areas” to grassland or heathland as appropriate using locally sourced seed/vegetation. However, we have not located a plan of these “agreed areas”. We advise that a nursery is commissioned to grow this material especially for the project as local provenance stock is unlikely to be widely available. Also, the subsequent section on turf management appears to propose a different method to restore damaged areas, but we presume that this would apply across the wider development site. Clarification is required on this. | Heath habitat restoration is proposed within the maritime grassland / scrub mosaic habitat where the boundary of the Onshore Development Area overlaps the SAC/SSSI. Grassland outwith the boundary of the SAC/SSSI is currently managed by mowing and will be restored using the methodology outlined in the Turf Management Plan. Further details are provided in Section 6 of the Terrestrial Ecology Assessment Update.
117. The reference in the Terrestrial Ecology Assessment update to habitat recovery being possible assumes that there will still be a source of propagules. However, during the construction/installation phase, vegetation and pockets of soil with seeds may be lost from the cliffs. If this is the case, recovery could take a considerable time. Mitigation to reduce this loss should therefore be considered as part of the Method Statement. | Works on the cliff will be undertaken by hand to minimise impacts and will be supervised by a suitably qualified ECoW. Further details are provided in Section 6 of the Terrestrial Ecology Assessment Update.
118. We note the statement in the Terrestrial Ecology Assessment update that works to undertake biodiversity net gain would be reliant on both survey and consultation with NRW and would welcome engagement in such discussions. | An Outline habitat enhancemen plan (document MOR-RHDHV-DOC-0169) has been agreed with NRW.
119. Table 19-16, Chapter 19 of ES Volume I (MOR/RHDHV/DOC/0100, F3.0, July 2019) refers to removal of 900m³ of material for HDD or 8,800m³ for trenching. We previously sought clarification on where this will be stored. If the trench is 10m wide x 550m long, soil storage will require a very large area which had not, to our knowledge, been identified. This could have impacts on protected habitats and species such as chough. The Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) states that Drawing 2 (Ref: 122938-BVL-Z0-00-DRZ-00003) now shows stockpile areas. However, we remain concerned that these may not be adequate unless only very small sections of trench are to be opened at any time. | The project engineers have confirmed that these areas are adequate to store all the spoil generated during construction works at the cliff top as only small sections of trench are to be opened at a time.
120. Paragraphs 212, 223 & 369, Chapter 19 of ES Volume I (MOR/RHDHV/DOC/0100, F3.0, July 2019) state that permanent habitat loss may occur on the cliff face. We suggest that this should read “will occur”. Decommissioning may cause more damage in the future and would need separate assessment. | As noted in the comment below, the impacts are assessed as long term in the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110) due to refined decommissioning methodology.
121. Section 6.1.2 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) and the Cliff Habitat Design Refinement note (MOR-RHDHV-DOC-0135, F1.0, 03/07/20) describe methods designed to reduce impacts and acknowledges that impacts will be long term, in excess of 40 years. This is an acceptable description of impacts. | Noted.
122. Section 6.1.2 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) also refers to seeding of stockpiles of soil in order to prevent dust/run off. This is a useful technique, but any stockpiles close to the SAC/SSSI should not be seeded with any non-native seeds which could be washed or blown into the SAC/SSSI and become established. Ideally, any grass used for this purpose should be a sterile hybrid to prevent production of seed which could spread. | Seeding would not be undertaken with non-native seed, and such provisions can be included within the EAP, to be agreed post-consent. This was agreed with NRW as shown in the Statement of Common Ground (document MDZ/L6).
123. Section 6.2.2 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20) describes turf storage and management measures; we are satisfied that these measures are appropriate. | Noted.
124. Section 9 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110, F1.0, 26/03/20), regarding conservation objectives for the SAC, has not referred to the SAC management plan so should be updated with reference to this document. | Version F4.0 of the Terrestrial Ecology Assessment update (MOR-RHDHV-DOC-0110), includes consideration of the SAC management plan.
Air Quality | This issue has now been resolved through ongoing engagement with NRW. NRW stated in their response dated 27th November 2020 to FEI under the TWAO process: "we note that the applicant has explained that the predicted traffic flows will be significantly below the screening criteria and therefore no LSE are predicted (ref. MMC-188 MOR-RHDHV-DOC-0148, v.F1.0, 18/09/20). The applicant also confirms that there are no other major projects that are anticipated to increase traffic flows to result in the screening criteria being exceeded. The Holyhead Eco Park biomass facility, although granted permission, is currently on hold so there is no predicted overlap with the MDZ at present. The applicant confirms that if they were to overlap, the biomass facility would require an Environmental Permit to operate and would be required to meet specified emission limits to prevent significant impacts to receptors. We currently have no further comment to make on in-combination air quality impacts."
125. We note that the ES Volume I, Chapter 4: Project Description (MOR/RHDHV/DOC/0004, F4.0, Oct 2019) includes reference to marine vessels associated with the device and cable installation, maintenance and decommissioning. However, no further information on likely vessel movements, numbers or associated emissions has been included in the Traffic Clarification Note. We therefore seek clarification on these as aerial emissions from boat-based transport are likely to require consideration within the ES air quality assessment.
126. Considering the Wealden case and the Dutch Nitrogen European Court of Justice rulings, we maintain our advice that further evidence is required as to why an in-combination air quality assessment is not considered necessary.
9.0 Seascape and Landscape
ES Volume I, Chapter 24
127. Our remaining comments following review of the additional information are summarised as follows.
128. We note that Trinity House and the International Association of Marine Aids to Navigation and Lighthouse Authorities (IALA) have now confirmed their colour and lighting requirements for marine safety, as follows: | Acknowledged
• All surface-emergent devices would need to be marked yellow to be visible to people within the marine environment. This would comprise a 5m yellow band at both ends of devices with a horizontal form and a 5m yellow band above water level for devices with a vertical form. The remaining areas of the devices would be grey, which is a more neutral, recessive colour.
129. The requirement for yellow markings to ensure devices are visible does not assist the development’s visual integration. The requirement for night-time lighting would continue to introduce night-time effects that would be seen from within the AONB. We therefore consider that emergent devices would still be a visible feature from the Anglesey AONB coast and due to their physical form, number, pattern and spatial extent would contrast with the natural characteristics of the seascape. | Acnkowledged
130. We welcome the amendments made to the project prior to and since submitting the Marine Licence application. However, we consider that significant adverse residual effects upon daytime and evening views from the Anglesey AONB remain, which in turn means that the public’s enjoyment of the AONB’s Special Qualities (expansive views/seascapes, and peace and tranquillity) would be significantly affected. We therefore maintain our significant concerns regarding the project. We advise that the residual impacts should be offset by developing and implementing an AONB landscape compensation package, in discussion and agreement with IoACC in consultation with NRW. | Acknowledged, the landscape compensation package is set out in the Section 106 Agreement.
131. ES Volume I, Chapter 4: Project Description (MOR/RHDHV/DOC/0004, F4.0, Oct 2019) describes the physical characteristics and number of components required. However, it should be ensured that Table 4-1 Mitigation Measures Embedded into Project Design records all key measures that are discussed/will evolve in the Outline Landscape Management Plan (OLMP) (MOR/SLR/DOC/0002, F3.0, Feb 2020). | Acknowledged
132. We have received sufficient information to clarify which types of surface-emergent tidal device would fall within the category “no visually prominent emergent devices” and the development intent within the areas outside the eight subzones included within the development parameters. We advise that appropriately worded text and report/figure references would need to be added to a Device Deployment Protocol. We also suggest the following be considered as conditions on the most appropriate consenting regime: | Acknowledged
• Detailed sub-zone development proposals to be submitted to IoACC in consultation with NRW for approval in advance of deployment via a Device Deployment Protocol.
• Monitoring of the effects of development within the seascape on the AONB. This is a new and novel project within a coastal AONB from which there are likely to be lessons learned. Monitoring could include, for example, the review of day and night-time effects of the first and every subsequent phase of tidal device deployment by comparing photomontages with the as-built development, appraising the nature of visual effects and reporting on the findings. The scope of the monitoring report and timescales for subsequent report submissions should be agreed with the IoACC in consultation with NRW.
133. The lighting conditions illustrated by the photomontage images suggest late afternoon soft lighting; the contrast is moderate to low. We do not consider these to be worst-case conditions for presenting the development’s visual effects. The photomontage images therefore cannot be relied on to determine the correct colour choice for minimising visual effects. We suggest that the following condition could be applied to address this: | Acknowledged, this could form part of the SLVIA work undertaken for each deployment.
• An environmental colour assessment is required to guide decisions on the use of colour for seascape integration.
134. We wish to make the following comments to strengthen the OLMP’s (MOR/SLR/DOC/0002, F3.0, Feb 2020) role in the commitment to the development’s seascape and landscape integration:
• The document should be renamed to include ‘seascape’ in the title. Despite what is set out in section 2, paragraph 18, the document discusses embedded mitigation for offshore components. Principles that are important to controlling the development’s visual influence offshore and onshore are best presented within a single document. We envisage this document being the primary means of clarifying the development parameters to future developers. | It is suggested that it remains titled "Landscape Management Plan" as it concentrates on the terrestrial elements of the Project. However, this can be altered if necessary.
• The document should be linked to the future phased planning and design of subzones with appropriate wording on the report cover, or boxed text on the first page, to make this clear. | Clarification needed
• Documents and figures relevant to SLVI development parameters should be listed within the OLMP. | It may be more appropriate to address this in the deployment specific SLVIAs that are required under the Device Deployment Protocol.
• Section 2.1.1. Offshore Project Components Visible from Land: “Visually Prominent” is explained in paragraphs 19 and 20 as a parameter to control the visual influence of tidal devices. We require an additional paragraph, as follows: “Note, the term “visually prominent” is used in this instance as a scale of visual effect that draws attention. This might occur because of the type of device, or the cumulative effect of multiple devices”.
• Paragraph 21 states: “A minimum separation distance of 1km will be applied from the coastline for Visually Prominent devices, helping to increase the separation distance between such structures from the coastline”. Please note that 1km is not a distance at which we have evidence to suggest prominent devices become acceptable within seascape views. In this case, we understand that the location of the tidal resource made it operationally difficult to create a greater separation distance than 1km from the coast. We advise that this is clarified in paragraph 21. | Agreed
Paragraph 28: Layout guidance to reduce visual prominence is welcomed, but we require clarification of how this principle would be effectively secured and delivered by future developers. | As a minimium the effects of any deployment would need to be consistent with those identified in relation to the PDE. Reductions in visual prominence could be identified through deployment specific SLVIA and secured through the Device Deployment Protocol.
A section describing the Cable Landfall development is required for completeness. Some thought is required about the visual integration of the cables at the top of the cliff and how this can be achieved (should HDD not be feasible), given the reinstatement of SAC/SSSI habitats precludes taller screening vegetation. | Agreed, this can be included in the Landscape Management Plan.
• Section 2.1.6. Across the Onshore Development area: We advise that an additional bullet point is added to ensure appropriate attention is given to development components i.e. “Use of colour and materials within the development to benefit visual integration”. | Agreed, this can be included in the Landscape Management Plan.
• Section 3.2. Protection and retention of existing vegetation. Paragraph 44 states: “All vegetation outside of the ODA boundary would be retained and protected using appropriate measures where necessary”. We require clarification of the “appropriate measures” that would be available for this. | Agreed, this can be included in the Landscape Management Plan.
• Section 3.4. Vegetation removal: The Holy Island Coast SAC/SPA/SSSI and its landcover features and sensitivities should be explained, and co-ordination is required between ecological restoration principles and landscape mitigation of the landfall cables (if HDD is not feasible). | Agreed, this can be included in the Landscape Management Plan.
• Section 3.6. Outline Specification: We advise that watering in of new planting to field capacity makes a big difference to establishment and should be added to the outline specification. | Agreed, this can be included in the Landscape Management Plan.
• Section 3.6.2. Cloddiau and Stone Walls: Controls are required to enable the restoration of boundaries to a good standard of workmanship. In the case of stone walls, the contractor should be a professional member of the Dry-Stone Walling Association. | Agreed, this can be included in the Landscape Management Plan.
• Section 3.6.4. Tree and shrub planting, paragraph 72: Given that the layout plans for the substation are indicative, we cannot preclude the requirement for shrub and tree planting where it would have a positive effect on the integration of the development. We advise that the last sentence is reworded to avoid an approach tied only to plant replacement. | Agreed, this can be included in the Landscape Management Plan.
• Section 3.8. Replacements: We advise that ‘failing to thrive’ is included in the list of reasons for plant replacement. | Agreed, this can be included in the Landscape Management Plan.
135. The OLMP currently relates to the onshore development and is concerned with reinstatement following construction disturbance and providing the landscape integration of new structures. Opportunities for local enhancement by improving species diversity will also be considered, which follows good landscape mitigation/development integration practice. However, considering the residual significant effect on the AONB, additional measures could provide some compensation for the development impacts. We suggest the following condition could be applied to address this: | -
• Detailed landscape scheme, materials, colour and lighting proposals to be submitted for all onshore development components and agreed with IoACC in consultation with NRW prior to their deployment. | Agreed (although this is a planning issue as opposed to ML) this is covered by proposed planning conditions and the consultation elements have been agreed between NRW and IACC.
136. Regarding the Cumulative Impact Assessment Matrix (MOR-RHDV-DOC-125 (3), F3.0, 07/03/20), we welcome a cumulative SLVIA to ensure seascape change in north-west Wales is recorded. | Noted
10.0 Cumulative Impacts
ES Volume I, Chapter 26
137. Our remaining comments following review of the additional information are summarised as follows. | see responses below
138. A dedicated signposting document and addendum to the ES CIA chapter has now been provided explaining how our previous comments on the cumulative/in-combination assessment have been addressed. This explains why the conclusions of the respective assessments remain unchanged despite updates to the plans/projects that have been considered. The additional information that has been provided in the PDE Matrix Spreadsheet (MOR-RHDHV-DOC-0127, F1.0, 22/05/20) is also helpful. | Noted
139. We welcome the addition of a measure of the Zone of Influence for each of the receptors that have been assessed. This clarifies the rationale for including/excluding plans/projects within the cumulative and in-combination assessments. | Noted
140. Similarly, we welcome the submission of an addendum to the CIA chapter which signposts where additional information has been provided and how this affects the conclusions of the respective assessments. | Noted
141. A small number of inconsistencies remain between the plans/projects included within the original assessments (largely documented in ES, Chapter 26: Volume I, II, III: Cumulative, Transboundary and In-Combination Impact Assessment and the Applicant’s Statement to Inform the Habitats Regulations Assessment), and those that have been screened in or out within the current CIA matrix (MOR-RHDHV-DOC-0125, F3.0, 07/03/20). This includes, for example, Ormonde Offshore Wind Farm which was not considered within the original assessments. We advise that all such changes that have occurred throughout the application process are fully documented within the CIA addendum (MOR/RHDHV/DOC/0133, D1.0, 03/07/20). This is required to provide a complete and transparent audit trail as to how all the relevant plans/projects have been included within the determination of potential cumulative/in-combination effects. | Ormonde OWF is included in the CIA matrix which shows that it was not included in the ES as it is deemed to be part of the baseline having been operational since 2012. It has been screened into the HRA but Table 8-14 explains that it is not considered further in the assessment due to being part of the baseline. Therefore the assessments are consistent.
142. In this context it is also important that the CIA screening matrix (MOR-RHDHV-DOC-0125, F3.0, 07/03/20) is fully comprehensive. For example, the Holyhead Breakwater remains missing from the CIA matrix despite it being considered within the applicant’s Water Framework Directive compliance assessment (09_MOR-RHDHV-APP-00126a, F4.0, 25/03/20). This also contradicts comments from the applicant as to why they believe that the Holyhead Breakwater is not required to be included within the cumulative and in-combination assessments. | Holyhead Breakwater has been added to the Matrix. This project was not included in the ES CIA as there was insufficient detail available at the time of writing. The project is listed in paragraph 161 of the WFD, noting it is only at the screening stage. The subsequent paragraphs then show it is not considered further, this is due to the insufficient detail available at the time of writing.
143. In addition, we consider that there remain projects that should be considered within the respective assessments. These include Awel-y-Môr offshore windfarm (the extension to Gwynt-y-Môr) and Minesto Phase II as these projects are reasonably foreseeable and whilst consent may not yet be applied for/started, we consider that they are well-defined and there are well-founded reasons for believing that they will be taken forward. | Awel-y-Mor has been added to the matrix , noting that there were insufficient details to assess this project at the time of the Morlais ES (and still are). It is therefore the reponsibility of new projects such as Awel-y-Mor to consider cumulative impacts with projects which are further progressed, such as Morlais. The full Minesto project is also included in the matrix.
144. An updated matrix with full reference to all plans and projects that have been considered within the CIA should be provided. This should be accompanied, as necessary, by an updated CIA addendum. Furthermore, topic-specific comments raised by NRW Advisory should be addressed within the respective assessments, including the WFD compliance assessment. This will help to provide further confidence in an updated CIA. | The Applicant has sought to address all NRW comments on topic-specific assessments and the CIA addendum (document MORRHDHVDOC0133(03)) provides a summary of any updates to the CIA as a result. This is supported by the CIA matrix (document MORRHDHVDOC0125(02))
145. Where topic-specific assessments are considered inadequate the same conclusion will apply to the respective in-combination/cumulative assessments. Any residual concerns will therefore need to be considered when evaluating the scale of potential in-combination/cumulative effects.

## FEI_ML001 ABPmer
FEI_ML001 ORML1938 – Consultation Response, ABPmer
Feedback | Response
1 Introduction
ABPmer was requested by Natural Resources Wales (NRW) to review the further information relating to underwater noise that has been submitted by the applicant for the Morlais Tidal Stream Demonstration Project. The review has considered how the potential effects from underwater noise have been considered and if the original concerns and recommendations that were provided in the previous underwater noise advice note (ABPmer, 2020) on the Environmental Statement (ES) and Appendix 12.4 - an underwater noise technical note have been addressed. In particular, this review has focused on the following additional documentation that has been submitted by the applicant: | N/A
 Outline Environmental Monitoring and Mitigation Plan (MOR-RHDHV-DOC-0072); | N/A
 Fish Ecology Issues Response to NRW comments (MOR-RHDHV-DOC-0114);
 Underwater Noise Modelling Report (MOR/RHDHV/DOC/0116);
 Marine Mammals Underwater Noise Modelling Note (MOR-RHDHV-DOC-0117);
 Signposting for responses to ORML1938_ABPmer (MORRHDHVDOC0127);
 Fish Ecology Response to ABPmer comments (MOR-RHDHV-DOC-0127a); and
 Addendum to the CIA Chapter (MOR-RHDHV-DOC-0133).
2 Review Findings
In terms of underwater noise, the applicant has responded to and addressed all the significant gaps that were identified in the previous review of the Morlais Tidal Stream Demonstration ES (ABPmer, | Noted
2020). The further information that has been provided is considered to be broadly adequate in terms of the modelling and assessment approach, and the cited evidence base. The key findings of the review are discussed below.
2.1 General
The recommendations provided in the previous review (ABPmer, 2020) have been considered by the | Noted
applicant. Site specific underwater noise propagation modelling has been undertaken (Document Ref:
MOR/RHDHV/DOC/0116). The acoustic models that have been used and underlying assumptions are set out. The model input parameters are clearly presented, including source noise levels, frequency content, seabed properties and the sound speed profile in the water column. Full account is also taken of the complex bathymetry at the Morlais project site and surrounding area.
2.2 Fish and shellfish ecology
The gaps that were identified in the previous review of the fish and shellfish ecology assessment have been addressed or adequate justification for not doing so has been provided. | Noted
The applicant has undertaken a detailed review of the potential effects of particle motion on fish and | Noted
shellfish based on the latest available scientific evidence (Document Ref: MOR-RHDHV-DOC-0114).
This review acknowledged the difficulty in measuring and modelling particle motion, the lack of experimental data on the responses of fishes and invertebrates to potentially damaging levels of particle motion, and the absence of guidelines on the levels of particle motion that are likely to have adverse effects. In light of these limitations, the conclusions of the review are considered fair and reasonable.
An explanation for not assessing the potential consequences of underwater noise impacts on fish populations has been provided (Document Ref: MOR-RHDHV-DOC-0127a). It is agreed that there are no readily available predictive models that could be applied to fish to determine potential effects of disturbance on life functions. However, Popper et al. (2014) provide qualitative thresholds for effects of underwater noise on fish eggs and larvae which could be applied to inform the potential consequence to fish populations. It is noted that the potential effects on fish eggs and larvae based on Popper et al. (2014) are included in the further information provided by the applicant (Document Ref: MOR-RHDHV-DOC-0127a) and therefore the issue is considered to have been appropriately addressed. | Noted
2.3 Marine mammals
The issues that were raised in the previous review of the marine mammal assessment have been addressed by the applicant in the updated underwater noise assessment (Document Refs: | Noted
MOR/RHDHV/DOC/0116 and MOR-RHDHV-DOC-0117). In particular, the latest published marine mammal injury criteria (Southall et al., 2019) and widely accepted behavioural disturbance criteria (Southall et al., 2007; Hastie et al. 2018) have now been applied. In addition, the cumulative exposure based on a realistic fleeing response has been evaluated to provide some context to the worst case assessment of a marine mammal remaining stationary for a period of 24 hours.
The cumulative noise effects assessment (Document Refs: MOR-RHDHV-DOC-0117 and MORRHDHV- | Noted
DOC-0133) is also considered to be acceptable. It is understood that the use of explosives underwater is no longer an option for the Wylfa decommissioning project and the use of explosives or
UXO clearance is not required for Morlais, and therefore this no longer needs to be considered in the in-combination assessment for marine mammals.
A couple of additional queries, however, have been identified in the updated underwater noise assessment which will need to be clarified by the applicant to ensure that the conclusions are based on worst case assumptions. These are detailed below. | See below
In Section 3.1.4 on page 8 of the underwater noise modelling report (Document Ref: MOR/RHDHV/DOC/0116), it is stated that “The Lofitech Seal Scarer has been used to model the effect of ADDs at the MDZ as it is one of the loudest ADDs on the market”. There are a number of ADDs that have reported higher source levels than the Lofitech Seal Scarer, including the Airmar dB Plus II, Ace Aquatec Universal Scrammer 3 and Ferranti-Thomson 4X which all have reported root mean square (RMS) source levels exceeding 190 dB re 1μPa m (MMO, 2018). It would therefore be helpful for the applicant to clarify if the Lofitech Seal Scarer can be considered a representative worst-case scenario given that there are other known ADDs with higher source levels. Despite this discrepancy, it is noted that the use of ADDs will be evaluated in more detail post consent in consultation with NRW and therefore the information that has already been provided by the applicant can be further developed and built upon once a suitable ADD has been selected. | It is the intention of the Applicant that the ADDs and disturbance range of the ADDs would be determined to the lowest source level possible that would ensure the marine mammal is beyond the range of potential collision risk, but without causing any significant disturbance or increased collision risk with other devices. Therefore the noise levels modelled are deemed to be conservative worst case scenarios. As noted by ABPmer, the details of the proposed use of ADDs will be considered during the development of the final EMMP, in consultation with NRW. It is important to note that, ADDs would only be activated if marine mammals were in close proximity and there is a potential risk of collision. The type(s) and number of ADDs to be deployed would be based on the latest technology and information to ensure adequate and effective mitigation.
In Section 3.2.1 on page 11 of the underwater noise modelling report (Document Ref: MOR/RHDHV/DOC/0116), it is stated that “The noise sources in this study are all considered nonpulses.” The noise generated by the proposed drilling and tidal devices are indeed considered nonimpulsive noise sources, although it is noted that percussive drilling has the potential to also be considered an impulsive noise source. However, Acoustic Deterrent Devices (ADDs) are generally considered an impulsive noise source (Dekeling et al., 2014). This is supported by the further information that has been provided by the applicant on fish and shellfish (Document Ref: MORRHDHV- DOC-0127a) which considers ADDs to be “impulsive noise as opposed to continuous noise”. It would be helpful to provide further information on the particular noise characteristics of the ADD that has been modelled (Lofitech Seal Scarer), such as the likely duration, rise-time, sound pressure impulse signature. This would help to confirm whether it would be more appropriate for it to be considered an impulsive noise source and for the underwater noise assessment to be based on the more stringent Southall et al. (2019) assessment criteria for impulsive noise, particularly given that worst case assumptions should form the basis of the assessment. | There is a commitment in the oEMMP that the underwater noise from ADDs will be reviewed as part of the ongoing development of the EMMP to ensure there is no significant disturbance or adverse effects. As outlined in the NRW closing [Inquiry Doc - 148] in relation to underwater noise including ADDS, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
It is understood that the Marine Mammal Mitigation Protocol MMMP, as part of the EMMP, will be based on the latest noise modelling (Document Ref: MOR/RHDHV/DOC/0116) to ensure adequate and effective mitigation. The issues noted above regarding the assessment of the effect of ADDs will therefore need to be clarified by the applicant before the proposed mitigation can be confirmed as | Responses provided above
acceptable.
2.4 Other species
The applicant has provided some further clarification on the potential effects on basking sharks. The | Noted
approach that was undertaken for assessing the potential effects of underwater noise on fish and shellfish was based on an assessment of the most sensitive species i.e. the worst-case effects. Basking shark is a less sensitive species, and therefore the magnitude of any effects are lower than those assessed for the most sensitive species. This approach is considered acceptable.
The applicant has also given some further consideration of the potential effects on marine reptiles. It is agreed that marine reptiles are transient visitors to the Irish Sea and their density within Welsh waters is low. There is also significant uncertainty in the hearing capability of turtles. Despite this, as species which migrate large distances, they are unlikely to be affected by highly localised noise disturbance in an area of open sea. The conclusion that there is therefore no potential for significant impact is considered reasonable. | Noted

## FEI_ML002 BEIS
FEI_ML002 ORML1938 – Consultation Response, BEIS
Feedback | Response
Good afternoon, | Noted 1. Morlais met with BEIS offshore renewables decommissioning team on 20/01/2020. The meeting was conducted by teleconference. The meeting was attended by Meggan Meek and colleagues on the phone call from the offshore renewables decommissioning team. 2. The agenda covered the following topics: a. Introductions b. Introduction to Morlais project c. BEIS Guidance Notes for Industry d. S.105 notice e. Next steps
Thank you for your email regarding the Marine license application for Menter Môn Morlais.
We would like to highlight Menter Mon Morlais responsibilities as a test centre for the decommissioning of their central infrastructure and their tenants infrastructure under the Energy Act 2004.
The Decommissioning of Offshore Renewable Energy Installations under the Energy Act 2004; Guidance Notes for Industry provides further guidance to assist developers/owners in understanding their obligations under the decommissioning scheme.
BEIS requires offshore renewable energy test centres in England and Wales to take responsibility for any central infrastructure and for the decommissioning of their tenants infrastructure. Test centres are requires to ensure that this is undertaken in line with all relevant legislation, licences and permits
The onus is on test centre owners to put in place robust arrangements to ensure responsible decommissioning of their tenants’ devices and associated infrastructure. It is expected that test centres will make their own decommissioning arrangements with their tenants, including appropriate financial and contractual arrangements to ensure the timely and safe removal of assets. Owners of test centres should submit decommissioning programmes to BEIS for their central infrastructure. This should also set out how they will ensure that the overall site is returned to its natural state at the end of its operational life.
If you require any further clarification regarding test centres and their decommissioning responsibilities which the Energy Act 2004 and Guidance Notes for Industry do not cover please e-mail the OREI Decommissioning team at the below e-mail.

## FEI_ML003 GAPS
FEI_ML003 ORML1938 – Consultation Response, GAPS
Feedback | Response
Thanks for this. There's been considerable progress since my original response, with submission of the Setting assessment, an update to the archaeological assessment, terrestrial geophysics and trial trenching all completed. As things stand, all my concerns have been addressed (including agreement on the significance of the setting impacts). For the terrestrial work, we are now at the stage of agreeing draft condition wording for the deemed planning consent; I've no additional comments on the offshore elements, unless/until we get to a similar stage for the marine licence and/or input is needed for the EEMP etc. | Noted

## FEI_ML004 JNCC
FEI_ML004 ORML1938 – Consultation Response, JNCC
Feedback | Response
Thank you for consulting JNCC regarding additional information to accompany the Environmental Statement (ES) received from Menter Môn Morlais Limited, which we received on 22 July 2020. | N/A
The advice contained within this note is provided by JNCC as part of our statutory advisory role to the UK Government and devolved administrations on issues relating to nature conservation in UK offshore waters (beyond the territorial limit).
JNCC were consulted on the above-mentioned ES in November 2019, and deferred comment at that point to NRW due to its inshore location (3 December 2019). The proposed project is located within the boundary of the North Anglesey Marine Special Area of Conservation, designated for harbour porpoise. This site extends into offshore waters and is jointly managed by JNCC and NRW. Following concerns highlighted by NRW during the previous consultation, JNCC provide the following advice in relation to potential impacts to this site from the proposed project. We also provide advice in relation to cetacean European Protected Species (EPS) which occur in offshore waters and may be impacted by the project.
Scope of works | The design envelope and approach to assessment is not unprecedented, the same approach was taken for the consented Perpetuus Tidal Energy Centre.
The breadth of the design envelope presented in this application and the potential number of tidal devices that could be deployed are unprecedented. This has resulted in a wide range of deployment scenarios being assessed, with no indication of which would be the most likely to materialise.
Our key concern regarding marine mammals from this project relates to potential collision with operating tidal devices. The lack of project detail makes it impossible to confidently conclude what potential impacts this project may have on marine mammals and subsequently a detailed mitigation and monitoring plan must be agreed before any consent can be granted. | As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148: https://www.dropbox.com/s/ss3831dg1rszuqg/Morlais%20Closing%20-%20NRW.pdf?dl=0] further progress has been made during the course of the Inquiry, including updates to the oEMMP and draft conditions. As concluded in NRW closing paragraph 37: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision-maker that there would be no such adverse effect."
North Anglesey Marine SAC | N/A
The proposed development is located within the North Anglesey Marine SAC, designated for harbour porpoise. This site includes territorial and offshore waters and is jointly managed by JNCC and NRW. Harbour porpoise have been found in particularly high densities between March and October.
The species’ Favourable Conservation Status (FCS) in UK waters is unknown. Lowered estimates of density in the Celtic and Irish Seas between decadal surveys (SCANS II and III) together with indication that harbour porpoise bycatch in the Irish and Celtic Seas is likely exceeding set conservation objectives, give us cause for concern that the population in this region might be vulnerable to further pressures. | Marine mammal collision limits have been agreed with NRW which takes into account the size and vulnerability (PBR) of marine mammal populations, as part of the ongoing development of the oEMMP.
We advise that adverse effect on site integrity cannot be ruled out due to risk of collision without an adaptive management process that ensures effective monitoring and a commitment to cease operating if an agreed threshold is breached. The monitoring system must be reviewed real-time to enable immediate action should an animal approach a device. The draft monitoring and mitigation document provided does not include such provisions. | The Outline EMMP (version 9) has been developed in consultation with NRW. This provides an adaptive management process to ensure there will be no adverse effect on site integrity, including real time monitoring in accordance with advice received from NRW. As concluded in the NRW closing to the TWAO Inquiry: "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision-maker that there would be no such adverse effect."
European Protected Species | The Outline EMMP (version 9) incorporates thresholds as advised by NRW in their Advice to Morlais on pre-consent assessment of collision risk and adaptive management (dated 13/05/20). These thresholds take into account the size and vulnerability (PBR) of marine mammal populations, as part of the ongoing development of the oEMMP. As discussed above, this provides an adaptive management process to ensure there will be no adverse effect on site integrity, including real time monitoring in accordance with advice received from NRW.
All cetaceans are listed as European Protected Species (EPS) and protected from death, injury and disturbance throughout their natural range. We advise that an offence, as defined in Regulation 45 of The Conservation of Offshore Marine Habitats and Species Regulations 2017, cannot currently be ruled out due to risk of collision without an adaptive management process that ensures effective monitoring and a commitment to cease operating if an agreed threshold is breached. Such thresholds would need to be species and population (Management Unit) specific; subsequently the monitoring system in place must be able to identify to a species level and be monitored real-time to ensure immediate action can be taken.
Collision risk modelling | Noted
JNCC are aware NRW have raised concerns regarding the assessment of collision risk. JNCC have discussed these with NRW and agree with their concerns and refer you to their comments.
Underwater noise modelling | There is a commitment in the oEMMP that the underwater noise from operational turbines and ADDs will be reviewed as part of the ongoing development of the EMMP to ensure there is no significant disturbance or adverse effects. As outlined in the NRW closing to the TWAO Inquiry [Inquiry Doc - 148] in relation to underwater noise, paragraph 46 states: "NRW is satisfied that these further commitments to adaptive management are an appropriate response to its concerns about the adequacy of the assessment work done to date in relation to the issue of underwater noise. As a result of these commitments, NRW advises the decision-maker than an adverse effect on integrity as a consequence of underwater noise can be ruled out at this stage."
Insufficient information is provided to enable a thorough assessment regarding operational noise, for example, array configuration, how many ADDs will be used, where will they be placed and interact with the devices and what influence scaling up the project have on noise levels.
Draft mitigation and monitoring plan | A draft Marine Licence condition has been proposed by the Applicant which requires the detailed EMMP to be agreed with NRW prior to deployment. The members of the Advisory Group must be agreed with Regulators as stated in the OEMMP. It is therefore the Applicant's position that this should not need to be stated in the consent to allow the membership of this group to be amended if required, without variation to the Marine Licence.
We acknowledge that the level of detail required to finalise this document is not available pre-consent. Subsequently we request a condition is attached to any consent issued stating no construction or deployment can be undertaken without an approved EMMP. We note the applicant proposes an advisory group review the outputs of the EMMP and discuss potential amendments. The key members of this group should be stated in the consent i.e. the regulator and appropriate SNCBs (NRW and JNCC). Development of the project is planned to occur in phases; the consent should also stipulate the plan must be reviewed before all subsequent deployment or construction can begin and any updates approved by the advisory group.
We note the list of potential mitigation and monitoring options described in the draft document. We agree device modification or removal should be on this list, however there is no mention of shutting down/switching off devices. Modification or removal of a device will take time to plan, so it is essential the devices in question are not operating during this period. This must be clear in the plan. | Plate 2-3 of the Outline EMMP (version 9) shows that if the number of collisions has reached a species threshold turbines would cease operation at the first safe opportunity.
The option of shutting down all devices must also be included, and it be acknowledged they may not be able to operate again that year. A collision threshold must be agreed, which if breached would result in the shutting down all devices. Without this, we advise a conclusion of no adverse effect to site integrity cannot be reached. | Plate 2-3 of the Outline EMMP (version 9) shows that, following the situation described above, operations would be reviewed with NRW and the Advisory Group. Section 4.1 of the OEMMP describes mitigation measures, including a final failsafe to prevent an adverse effect from occurring. Such a failsafe is likely to be the cessation of operations of the tidal device.

## FEI_ML005 LPA (IoACC)
FEI_ML005 ORML1938 – Consultation Response, LPA (IoACC)
Feedback | Response
Marine and Coastal Access Act 2009: Part 4 Marine Licensing | N/A
ORML1938 Application from Menter Môn Cyf for a Marine Licence under Part 4 of the Marine and Coastal Access Act 2009 to undertake the Morlais Tidal Stream Demonstration Project located to the West of Anglesey
Further to your invitation for comment on the further information that has been submitted by Menter Môn Morlais Limited in relation to the above application, the Isle of Anglesey County Council (hereafter referred to as ‘the Council’) has now had the opportunity to review the further information and has the following comments.
Please note that this representation is made without prejudice to any further comments that the Council may subsequently wish to make, including upon receipt of further or more detailed information. | N/A
The Council confirms that is also a statutory consultee for the application for an Order under the Transport and Works Act that has made by Morlais to the Welsh Ministers. The Council therefore confirms that it has confined this response to matters which would be controlled through the licence or which are relevant to that determination, and not issues currently being discussed in other consenting processes. | N/A
The Council refers to its previous comments in its representation dated 17th December 2019 which confirms the due to the proposed works having both terrestrial and marine elements, consistency and clarity is required across the marine elements (including intertidal works) which forms part of any Order given under the Transport and Works Act, and any Marine Licence approved. This is critical in order to ensure effective discharge, monitoring and enforcement. | The interrelationship between the Order, Marine Licence and the deemed planning permission was addressed in a note prepared by Eversheds Sutherland and submitted to the TWAO inquiry. As recorded in Menter Mon’s closing submissions to the Inquiry there was no disagreement from any party with the note as presented, and indeed it was particularly welcomed by NRW advisory. The note explains how the Order and deemed planning conditions have been drafted to avoid conflicting regulatory function between the three principal consents that will govern the project. Menter Mon would agree that it is important to ensure that any conditions sought to be imposed on the Marine Licence in relation to the intertidal area are consistent with those proposed in the deemed planning conditions for the onshore works. Menter Mon note that there was no objection to the form of any proposed deemed planning conditions in so far as they relate to the intertidal area from any party, and would welcome the opportunity to discuss Marine Licence conditions with NRW Regulatory to ensure overall consistency is preserved.
Management Plans | The code of construction practice is specific to onshore works and would also include works within the intertidal area. The equivalent document for the offshore and intertidal works from a marine licensing perspective is the Construction Environmental Management Plan which is secured through condition 4 of the Marine Licence as well as Schedule 1 Part 4 of the draft Transport and Work Act Order. Both the draft ML condition and draft TWAO condition, require the Construction Environmental Management Plan to be approved by the Regulators prior to construction and Menter Mon would envisage that there provisions would be consistent as regards works in the intertidal area..
It should be noted that the condition that is proposed to be attached to the deemed planning consent (condition 03) has been amended by Morlais to confirm that separate Code of Construction Practices will be submitted for the onshore phases of the Morlais Project. This should also be aligned with the relevant condition attached to any Marine Licence which confirms the need for the develop to submit a CoCP prior to commencement of that phase of the works affecting the intertidal area and the subsequent need to carry out that phase of the work in accordance with the relevant approved CoCP.
02 ES Chapter 4 Project Description MOR/RHDHV/DOC/0004 | The Council subsequently withdrew its objection to the Order by letter dated 27.11.20
03 ES Volume II Chapter 4 Figures - Zoning MOR/RHDHV/DOC/0101
The Council notes that the Document ‘ES Chapter 4 Project Description’ has been updated to outline the design development and refinements since the ES was submitted, and to present an update to the Project Design Envelope.
The Council confirms that while these changes do not fully address its concerns that the restriction on installation of visually prominent devices in sensitive zones, which is included as embedded mitigation in the SLVIA, is not secured, further engagement with Morlais has identified a satisfactory resolution. That is, in addition to the Council being specified as consultee on any Device Deployment Protocol applications under the Marine Licence, it will also be specified as a required consultee in the TWAO. The Council is currently awaiting to review the revised Order to confirm that the wording that allows this consultation to take place is satisfactory. Should the TWAO be amended as requested, no further change would be sought to the proposed conditions of the Marine Licence.
Shipping and Navigation | The TWAO and ML secure a robust process for ensuring the navigational safety of all navigation users. This includes updated area wide Navigation Risk Assessments every 2 years and array specific navigation risk assessments before any devices are deployed. There will also be engagement with Trinity House with regard to appropriate navigational marking and lighting of the MDZ and associate devices and the development of an Emergency Response Co-ordination Plan. The applicant anticipates this development to provide real economic benefits to the region including the Port of Holyhead and will be encouraging devices developers and supporting services to use the port for construction, operational, and decommissioning phases. As the closest port to the development it is anticipated that many developers will want to operate marine activities from the Port of Holyhead.
20 Navigation and Shipping Responses MOR/RHDHV/DOC/0124
The Council has previously confirmed in its Representations that the Island’s tourism sector benefits significantly from the use of the local seas by a range of marine craft. The Council was therefore seeking confirmation that navigational safety in this busy section of sea would be maintained during all phases of the project. The Council also advised that it was seeking confirmation that the use of the Port of Holyhead will be maximised and how local economic benefits will be secured during the construction, operational, and decommissioning phases.
The Council welcomes the confirmation that following further engagement with stakeholders from the shipping industry, further mitigation has been proposed. The Council notes that this mitigation includes adjusting the western boundary of the area where only submerged tidal devices with a minimum under keel clearance (UKC) of 8m can be deployed, thereby increasing the area available for passage for small vessels and reducing the extent of visually prominent tidal devices and increasing their distance from shore. | Agreed
The Council notes that this change is reflected in the updated indicative Figures 4.1 to 4.5 provided in document no. MOR/RHDHV/DOC/0101. However the Council is concerned that these figures are indicative and that this change to the western area is not secured. The Council considers that this needs to be secured in the Marine Licence so that the mitigation it provides is not undermined through future devoice deployments. | The restricted areas, blue, green and gold, as detailed in document no. MOR/RHDHV/DOC/0101 are defined in the TWAO. The draft Marine Licence conditions proposed by the Applicant (Condition 27) secures the additional mitigation measures referred to in the Navigation Risk Assessment.
The Council also welcomes the confirmation in the document that the Promoter is committed to resolving the further concerns raised by key shipping and navigation stakeholders and that this engagement is on going. The Council will comment further once this engagement has been concluded and an update provided by the Promoter. | Noted
Archaeology and Cultural Heritage | Noted
The Council understands that NRW has consulted GAPS directly as a statutory consultee as part of this re-consultation. The Council confirms that GAPS is the regional curator with regulatory and advisory functions and is the Council’s advisor with regards to matters concerning archaeology. The Council therefore confirms that the comments provided directly to NRW by GAPS should be also considered as the Council’s comments in relation to matters concerning Archaeology and Cultural Heritage.
The Council is aware that GAPS has previously confirmed in its Representation to NRW (9th January 2020) that the proposed development has the potential for impact upon both marine and terrestrial elements of the historic environment. | The latest response provided by GAPS on 4th August 2020 confirms that their concerns have been addressed.
The Council and GAPS have previously agreed that it is satisfied that the archaeological mitigation for the intertidal zone is integrated to the terrestrial mitigation programme, adopting a principle of seamless management and will therefore provide comments on the intertidal archaeological elements of the project as part of its comments under the TWAO. | Noted
Seascape, Landscape and Visual Effects | Noted
As previously confirmed the Council has an interest in the direct and indirect effects of the proposed marine works on Landscape, Seascape and Visual amenity.
30 Seascape Landscape and Visual Impact Assessment - Post Application Consultation Responses MOR/SLR/DOC/0001 | Acknowledged
31 Outline Landscape Management Plan MOR/SLR/DOC/0002
The Council acknowledges that the ‘Seascape Landscape and Visual Impact Assessment – Post Application Consultation Response’ deals with some of the comments/requests for clarity as outlined in the Council’s representation to the TWAO (October 2019) and ML (December 2019) in relation to matters concerning SLVIA. This also sets out the outcome of the recent discussions that have taken place between the Promoter and Trinity House, which outcomes the Council very much welcomes.
The Council notes the commitment to marking 5m bands at the ends of each of the devices yellow, or a colouring band 5m high on hubs or similar vertically shaped infrastructure rather than colouring the whole device. The Council also notes the confirmation that that the detail of the marking required will depend on the design of the specific device or structure and that the extent of the yellow marking would depend on the design of the devices. The Council also notes the confirmation that the remainder of the devices would be coloured grey, although the exact colour would be agreed by a Marine Licence Condition. As previously requested, the Council, wishes to be consulted on this information when it is submitted under condition. | Acknowledged
The Council also welcomes the submission of the amended photomontages, which confirms the most recent commitment to the colouring of the tidal devices as a result of discussions to better define the requirements of Trinity House, as well as confirmation of the RAL colour that has been used for these images (both yellow and grey). The revised photomontages demonstrate that the adoption of the revised colour scheme design does lead to a reduction in the tidal devices’ visual prominence as experienced at viewpoints and by principal groups of onshore visual receptors in the closest part of the AONB. However, a significant adverse impact is still predicted and device deployments need to be set up to allow monitoring of that impact with regard to the details of the design of devices when that is known. The Council also accepts that the design of devices will evolve over time as this is a demonstration zone to test new devices. | Acknowledged
The Council also acknowledges that the deployment of devices within the Morlais Demonstration Zone is proposed to be controlled through approval under condition of a Device Deployment Protocol for each deployment. | Acknowledged
Further engagement with Morlais has confirmed that the Device Deployment Protocol will be subject to a condition attached to any consent given under both the TWAO and Marine Licence. As confirmed at the beginning of this representation, the Council has requested that the TWAO explicitly confirms that the Council as Local Planning Authority will be consulted as part of the process of discharging the relevant condition attached to the TWAO. Morlais have agreed to this arrangement and the Council currently awaits the receipt of the updated Order that will reflect this arrangement. | Acknowledged
From an SLVIA perspective, a key consideration will be to ensure that the Protocol contains a commitment and a simple process to assess cumulative impacts upon key seascape, landscape and visual receptors. These impacts will be incrementally generated by each proposed device deployment and should be assessed against a baseline of the currently operational and consented (by previous Device Deployment Protocols) deployments. This is necessary to ensure that the impacts remain within the assessed envelope. | Acknowledged
- Export Cable Landfall | Acknowledged
The Council acknowledges that the preference for the method of installation of the cable landfall is for Horizontal Directional Drilling, which would leave no visible infrastructure on the surface post construction. However, should this not be possible, the alternative method would be open trenching, cable protection and above ground cables attached to the cliff face, and this is the worst case used for the assessment. The cables pass through the intertidal area and the Council therefore suggests that alignment on the approval of controls for this work, including on the Code of Construction Practice required by the deemed planning permission onshore, with the controls of the Marine Licence would be advantageous.
It is noted that following preparation of the SLVIA, there has been a refinement of the proposed installation of trenched and above ground cables at Abraham’s Bosom. | Acknowledged
As previously noted in the Council’s Representation, there are some concerns about the potential visibility of the cabling as it emerges above the clifftop (max 7m width and 2m height) in the views of a small number of sensitive visual receptors. These works will be above mean high water and the Council is therefore addressing this element through the TWAO process not the Marine Licence. | Acknowledged, it is considered that these can be addressed through the Landscape Management Plan.
The Council confirms that it wishes to be consulted on the development of potential localised mitigation measures and the controls of intertidal works. | Acknowledged
- Construction Period – Lighting on vessels | Acknowledged
As confirmed by paragraph 43 of the response, the construction period is expected to overlap considerably with the operational phase. This will mean that vessel movements for the installation of the cable tail and the installation of the protection for the export cable with take place in each year during a 10-year period. This will result in the construction/support vessels (which would be illuminated at night) being seen in conjunction with operational tidal devices.
No information has been provided on the lighting requirements of these vessels. The Council requests that detail is provided regarding the lighting levels that such vessels would require to operate in the same manner as information upon lighting levels for the marker buoys that has been provided in the post consultation response. This would allow a better understanding of the spatial extent and intensity of the contribution of the support vessel(s) to overall potential lighting effects upon the AONB. | The number of construction vessels expected to be present was described in Document MOR/SLR/DOC/0001: Seascape Landscape and Visual Impact Assessment – Post Application Consultation Responses. The main construction and support vessels that would be present during the 10 year construction phase are those involved in inter-array cable installation (30.14% of the year), hub installation (49.32% of the year) and tidal device installation (throughout the year, with the potential for two additional vessels for 18% of the year). Therefore, it is expected that up to six vessels would be involved in these activities at any one time but there is potential for additional vessels to be present at any particular time (an expected maximum of 16 vessels). Additional vessels could comprise those involved in the installation of the cable tail and export cable and the installation of protection. However, the vessels involved in these activities are expected to be present for short parts of a given year during the construction phase; 5.48% (cable tail installation), 5.48% (export cable installation) and 3.29% (export cable protection installation). Overall, the expected maximum number of construction/support vessels that could be on site at any one time is 16. However, this concentration of vessels would only be present for a short part of the year and is also based on a worst-case scenario of the whole 240 MW being installed in one phase. As the construction would be based on a phased development a much lower number of vessels on site at any one time is likely to occur with breaks in activity between phases. The number of vessel days on site stated in the Environmental Statement is based on 24 hour working. Therefore, the vessel numbers stated above could be applicable at night (with associated lighting). It is possible that fewer vessels (than stated above) would operate at night as safer working conditions would occur during daylight hours, but it is not possible to be definitive about this as the detailed approach to installation will be developed by specialist contractors much closer to actual offshore works commencing. The judgements included in the SLVIA are based on full deployment of the devices assumed as part of the site design envelope throughout the operational phase. This comprises 130 surface emergent tidal energy devices and eight electrical hubs, concentrating on the main offshore components of the project. The SLVIA also assumed visibility of navigation lights on all the tidal energy devices with a visibility of not less than five nautical miles. However, subsequent consultation with Trinity House has meant that the lights on the tidal energy devices can be limited to 150m (i.e. less than the distance to the coastline). Significant effects were predicted at the closest light time viewpoints within the Anglesey AONB (Car Park at South Stack Light House and Ellin’s Tower). Beyond these viewpoints the potential effects reduced due to a combination of the intervening distance and the baseline context. These predicted effects took account the overlap between the construction phase and the operational phase, together with the likely presence of construction and service vessels at night. If necessary, further detail would need to be provided in relation to device specific deployments, when more information is known about construction requirements.
- Council’s current position with regards to the SLVIA | Acknowledged
While the Council very much welcomes the clarity that has been received following recent engagement between the Promoter and Trinity House regarding their requirement for the colouring of the tidal devices and the use of lighting, the SLVIA conclusion remains that the offshore components of the Morlais Project will have significant adverse effects on the Anglesey AONB and Holy Mountain Heritage Coast, two SCAs (SCA 31 and SCA 14) and six extensive groups of visual receptors. Many of the affected receptors are associated with Anglesey’s key tourist economy. As confirmed in its Representation (October 2019), the Council requires the securing of adequate compensation measures, including enhancement of features, to balance the effects of adverse impacts of the project as confirmed in the ES on Seascape, Landscape and Visual receptors.
The Council confirms that discussions regarding potential proposals for compensation measures are being progressed with the Promoter. The Council confirms that the agreed compensation proposals will be secured under the TWAO. The Council will liaise with NRW’s advisory function in relation to the detail of the compensation proposals once discussions have progressed between the Council and Morlais and the detail of the proposals available for consideration. | These details are included in the Section 106 Agreement.

## FEI_ML006 MCA
FEI_ML006 ORML1938 – Consultation Response, MCA
Feedback | Response
Following our response dated 7/1/20 (attached), we have had meetings with Mentor Mon and their consultants to discuss our concerns which have been recorded in meeting minutes. However, there is outstanding documentation to be formally submitted to show how these have been addressed – a NRA Addendum and revised EIA chapter would be the logical way forward. Although we are not raising an objection as such, our position is that we are unable to provide our formal agreement/acceptance of the marine licence application until we have seen, and are satisfied with, the additional information required. | The NRA Addendum (NRAA) and amended ES Chapter have been submitted and have been reviewed by the MCA so many of the points below have been addressed.
MARINE AND COASTAL ACCESS ACT 2009: PART 4 MARINE LICENSING | Noted
MORLAIS TIDAL ARRAY (MTA)
Thank you for the opportunity to comment on the Marine Licence application and supporting information for the proposed Morlais Tidal Array project to construct and operate the tidal devices west of Anglesey. The MCA’s remit for offshore renewable energy development is to ensure that safety of navigation is preserved, as progress is made towards government targets for renewable energy.
The Navigation Risk Assessment (NRA) and the shipping and navigation elements of the Environmental Statement (ES) have been reviewed and we would like to comment as follows: | Noted
NRA | The MGN 543 Checklist was included in the NRAA and was acknowledged in the MCAs Response to Statements of Case for the TWAO process where they stated. "A completed MGN Checklist was provided in Annex G."
The MCA is satisfied the NRA has been conducted in accordance with the published guidelines for the Methodology for Assessing Navigational Risk, with regards to the process undertaken. However, the completed MGN 543 Checklist has not been provided.
We are satisfied that appropriate traffic data has been collected in accordance with MGN543, which includes six months’ worth of AIS data in addition to the minimum AIS and radar data requirements. | Noted
Out of 46 hazards identified for collisions, contacts, groundings and snagging during the construction and operation phases, 26 hazards were assessed as having a risk score higher than 4 (‘low risk’). Therefore, these 26 hazards would require additional mitigation for the risk to be tolerable and As Low As Reasonably Practicable (ALARP). However, it is unclear based on the terminology used in the document, which mitigation measures are recommended. There is a ‘Suggested risk control’ section where mitigation is recommended however for the remainder of the document they are referred to as ‘possible mitigation’. In order to agree that risks are deemed to be ALARP, it needs to be made clearer exactly which risk control measures are recommended for implementation. | Details of Embedded Mitigation Measures and Additional Mitigation Measures have been discussed with the MCA and are included in the NRA Addendum, Amended ES Chapter and agreed in the MCA Statement of Common Ground (SoCG).
We would recommend that a section is included on interactive boundaries between the devices and shipping routes, particularly to assess the northern and eastern boundaries to provide evidence for the risk control measures. | Interactive Boundary Assessments for the northern and eastern boundaries have been completed and provided to the MCA.
The type of device(s) to be installed is not yet known and the report suggests that it would be a mixture of surface floating, mid-water suspension and bottom mounted. Feedback has been gathered from stakeholders (ferry companies, CoS, RYA and RNLI) on under-keel clearance requirements, however we would recommend that under-keel clearance calculations are made to corroborate this evidence. Further guidance is available from the MCA’s Under Keel Clearance paper, which can be found on our website: https://www.gov.uk/guidance/offshore-renewable-energy-installations-impact-on-shipping. | The methodology for calculating under keel clearance has been detailed in the NRA Addendum and the MCA SoCG
NRA Additional Mitigation
We have the following comments on the list of 15 Additional Mitigation measures in Table 11-1 for reducing the inherent risk to ALARP:
• “Restrict Navigation through the Morlais Zone” via an Area To Be Avoided or Precautionary Area. These are IMO routeing measures and will need a formal proposal to MCA and UK Safety of Navigation (UKSON) committee for approval. | We have been in discussions with the MCA regarding Additional Mitigation measures and amended measures are included in the NRA Addendum and MCA SoCG.
• “Exclusion of fishing within the Morlais Zone”. It is not clear how this is to be implemented. Whilst this risk control aims to prevent snagging of fishing gear, it relates to the risks associated with fishing activity rather than to surface navigation.
• “Establish no anchoring areas” around the nearshore cable route. This will need a formal proposal to MCA for approval.
• “Enhanced cable protection” where burial is not possible. It can be argued this is an embedded risk control since it is already a requirement to protect unburied cables.
• “Construction vessels to be marked in accordance with COLREG”. It can be argued this is an embedded risk control since the Collision Regulations are an established set of regulations for shipping activity and all vessels, when not jacked up, must already exhibit signals in accordance with COLREG. When any construction vessel is jacked up, it must exhibit signals in accordance with the UK Standard Marking Schedule for Offshore Installations.
Environmental Statement (Shipping & Navigation Chapter) | We have been in discussions with the MCA regarding Additional Mitigation measures and amended measures are included in the NRA Addendum and MCA SoCG.
The ES does not make any proposals on risk controls, rather it uses the ‘possible mitigation’ terminology and it is therefore unclear what is being proposed.
The list of mitigation measures in the ES differs from that in the NRA: | This has been clarified in the NRAA and agreed with the MCA in their SoCG.
• Within the NRA it suggests: “Devices >20m below CD to be deployed within Zones 1,2 and 8”. The ES only suggests this for zone 1, not 2 or 8 so we request justification from Mentor Mon/Marine Space.
• “Re-design eastern boundary”. There should be an interactive boundary assessment on the inshore sea space to be able to discount reducing the eastern boundary as commercially unviable.
• It is not clear how much sea room there will be (RYA recommend 4 cables) east of the eastern boundary. However, we note that “Only deploy devices that allow at least 8 m
UKC along eastern boundary” as an additional risk control has been included which we would suggest requires an under-keel clearance calculation to support it.
It appears there are discrepancies between the NRA and Shipping & Navigation Chapter in the ES. Where the advice contained within the NRA has not been taken forward by the applicant into the ES, there should be appropriate justification to support it.
Risk Matrix | A risk matrix was produced and supplied to the MCA on the 19th June. This was updated and included in the Amended ES Chapter.
We note there are inconsistencies between the risk matrices in the NRA and ES. The NRA lists each hazard, scores them and lists possible risk control measures. The ES however, does not use the NRA hazard list, instead some of the NRA hazards have been included along with combined hazards which are described as ‘Impacts’ e.g. “Potential Impacts to Commercial Vessels”. These have then been scored. This makes it quite confusing and difficult to read and understand. The result is that the risk control measures do not correspond. For instance, the NRA lists seven risk controls for the Grounding of a Recreational Vessel, whereas the ES identifies just one risk control measure.
We request the applicant provides a risk control log of embedded and additional mitigation measures to confirm what is proposed for the project. Without this we are unable to agree that the risk scores are ALARP.
Cable Routes | Noted. The following will be included in the ML Conditions: The licence holder must not reduce water depth by more than 5% as result of cable protection activities (referenced to chart datum) and under no circumstances must depth reduction compromise navigational safety.
Export cable routes, cable burial protection index and cable protections are issues that are yet to be fully developed. However due cognisance needs to address cable burial and protection, particularly close to shore where impacts on navigable water depth may become significant. Any consented cable protection works must ensure existing and future safe navigation is not compromised. The MCA would accept a maximum of 5% reduction in surrounding depth referenced to Chart Datum. Existing charted anchorage areas should be avoided.
Safety Zones | Noted.
Construction and operational safety zones will only be granted subject to a detailed justification with significant evidence from the construction and operational phases in addition to the baseline NRA required supporting the case.
Mooring Arrangements | Noted. This is agreed in the MCA SoCG and will be included in the ML Conditions.
Third Party Verification of the mooring arrangements for all floating devices will be required prior to construction to provide assurance against loss of station. Ideally this will be a condition of the marine licence. Guidance on regulatory expectations on mooring arrangements can be found on our website: https://www.gov.uk/guidance/offshore-renewable-energy-installations-impact-on-shipping
Emergency Response | Obstructing access to harbour and safe havens is an event potentially leading to one of the scored hazards as detailed in the NRAA. Therefore, this was taken account of during the risk scoring process in the NRAA.
Stakeholders raised a concern about access to Holyhead as a safe haven however it is not clear where this has been addressed in the NRA and ES.
Further consultation will be required with the MCA to discuss emergency response requirements in accordance with MGN543 Annex 5, including the completion of a SAR Checklist. | Noted
Bathymetric Survey Data | Noted
MGN 543 Annex 2 Paragraph 6 requires that hydrographic surveys should fulfil the requirements of the International Hydrographic Organisation (IHO) Order 1a standard, with the final data supplied as a digital full density data set, and survey report to the UKHO and MCA for updating of nautical charts and publications. This should include the site and its
immediate environs extending to 500m outside of the development area and a cable route survey post-construction.
Turbine Layout Plan | Noted
The turbine layout plan will require discussion and approval of the MCA and Trinity House prior to construction commencing. This is to ensure risks to navigation safety and search and rescue operations are minimised.
Marine Licence Conditions | Noted
The MCA would expect the above comments to be addressed by the applicant before the MCA can confirm its support of the Marine Licence application. Once these has been discussed further the MCA would like to request the following navigations safety conditions and advisories are included in the Marine Licence:
Conditions | Noted the applicant has supplied draft ML Conditions for consideration which we believe address these requirements.
1. The Licencee must ensure appropriate steps are taken to minimise damage to the shoreline resulting from the works and that navigational aids and/or the topography are returned to the original profile, or as close as reasonably practicable, following the completion of the works.
2. The Licencee must issue local notification to marine users, including fisherman’s organisations, neighbouring port authorities, HM Coastguard, UKHO and other local stakeholders, to ensure that they are made fully aware of the activity at least 14 days prior to the commencement of the authorised project.
3. The Licencee must ensure that HM Coastguard, in this case nmoccontroller@hmcg.gov.uk, The National Maritime Operations Centre is made aware of the works prior to commencement.
4. The Licencee must notify the UK Hydrographic Office of the completion of the authroised project within 14 days to permit the updating of nautical charts and publications.
5. The Licencee must ensure that 'the works' do not encroach on any recognised anchorage, either charted or noted in nautical publications, within the proposed consent area.
6. Any consented cable/pipeline protection works must ensure existing and future safe navigation is not compromised. The MCA would accept a maximum of 5% reduction in surrounding depth referenced to Chart Datum but under no circumstances should depth reductions compromise safe navigation.
7. A Third Party Verification of the mooring arrangements for all floating devices must be undertaken prior to construction to ensure the mooring design is suitable for the location.
8. As per the requirements of MCA’s MGN 543 and supplementary updates, the Licencee must complete periodic hydrographic surveys of the consented area or subsections thereof, to the IHO Order 1a survey standard. On completion of these surveys the results and a corresponding report of survey must be supplied to the UKHO, with notification to the MCA Hydrography Manager.
9. The Licencee should ensure suitable bunding, storage facilities are employed to prevent the release of fuel oils, lubricating fluids associated with the plant and equipment into the marine environment.
10. In case of damage to, or destruction or decay of, the authorised project seaward of MHWS or any part thereof, excluding the exposure of cables, the undertaker shall as soon as reasonably practicable and no later than 24 hours following the undertaker becoming aware of any such damage, destruction or decay, notify MCA, Trinity House, the Kingfisher Information Service of Seafish and the UKHO.
11. No part of the authorised project may commence until the NRW, in consultation with the MCA, has confirmed in writing that a detailed cable laying plan has been satisfactorily conducted incorporating a burial risk assessment encompassing the identification of any cable protection that exceeds 5% of navigable depth referenced to chart datum and, in the event that any area of cable protection exceeding 5% of navigable depth is identified, details of any steps (to be determined following consultation with the MCA and Trinity House) to be taken to ensure existing and future safe navigation is not compromised or such similar assessment to ascertain suitable burial depths and cable laying techniques, including cable protection. This plan must include proposals for monitoring offshore cables including cable protection during the operational lifetime of the authorised scheme which includes a risk-based approach to the management of unburied or shallow buried cables.
12. In case of exposure of cables on or above the seabed, the undertaker must within three days following identification of a potential cable exposure, notify mariners by issuing a notice to mariners and by informing Kingfisher Information Service of the location and extent of exposure. Copies of all notices must be provided to the MCA, Trinity House, and the UKHO within 5 days.
13. No part of the authorised project may commence until the NRW, in consultation with the MCA, has confirmed in writing that the undertaker has taken into account and, so far as is applicable to that stage of the project, adequately addressed all MCA recommendations as appropriate to the authorised project contained within MGN543 "Offshore Renewable Energy Installations (OREIs) – Guidance on UK Navigational Practice, Safety and Emergency Response Issues" and its annexes.
14. Post construction monitoring must include vessel traffic monitoring by Automatic Identification System for a duration of three consecutive years following the completion of construction of authorised project, unless otherwise agreed in writing by the NRW. An appropriate report must be submitted to the NRW, Trinity House and the MCA at the end of each year of the three-year period.
Advisories
1. No radio beacon or radar beacon operating in the Marine frequency bands shall be installed or used on the works without prior written approval by OFCOM.
2. Any jack up barges / vessels utilised during the works/laying of the cable, when jacked up, should exhibit signals in accordance with the UK Standard Marking Schedule for Offshore Installations.
3. If in the opinion of the Secretary of State the assistance of a Government Department, including the broadcast of navigational warnings, is required in connection with the works or to deal with any emergency arising from the failure to mark and light the works as required by the consent or to maintain the works in good order or from the drifting or wreck of the works, the owner of the works shall be liable for any expense incurred in securing such assistance.
Conclusion | Noted
The comments detailed above are not considered to be blocks to development but provided to highlight areas of concern that must be addressed before any formal acceptance of the licence request.
Yours Sincerely,
Nick Salter

## FEI_ML007 MOD
FEI_ML007 ORML1938 – Consultation Response, MOD
Feedback | Response
Further to your e-mail below regarding the further information received, I can confirm that after investigation and review that the MOD has No Objection regarding this activity in the location specified. I hope this information is sufficient for your purposes. | N/A

## FEI_ML008 NATS
FEI_ML008 ORML1938 – Consultation Response, NATS
Feedback | Response
The proposed development has been examined from a technical safeguarding aspect and does not conflict with our safeguarding criteria. Accordingly, NATS (En Route) Public Limited Company ("NERL") has no safeguarding objection to the proposal. | Noted
However, please be aware that this response applies specifically to the above consultation and only reflects the position of NATS (that is responsible for the management of en route air traffic) based on the information supplied at the time of this application. This letter does not provide any indication of the position of any other party, whether they be an airport, airspace user or otherwise. It remains your responsibility to ensure that all the appropriate consultees are properly consulted. | Noted
If any changes are proposed to the information supplied to NATS in regard to this application which become the basis of a revised, amended or further application for approval, then as a statutory consultee NERL requires that it be further consulted on any such changes prior to any planning permission or any consent being granted. | Noted

## FEI_ML010 RSPB
FEI_ML010 ORML1938 – Consultation Response, RSPB
Feedback | Response
MARINE AND COASTAL ACCESS ACT 2009: PART 4 MARINE LICENSING | N/A
MORLAIS TIDAL ARRAY (MTA)
CONSULTATION ON FURTHER INFORMATION SUBMISSION
Thank you for consulting the Royal Society for the Protection of Birds (the RSPB) over the additional information for the above application.
Whilst we appreciate the further information provided, the RSPB continues to object to this application (and this response follows our recent objection to the Transport and Works Act (TWA) application). | N/A
We originally objected to the TWA application on the 31st October 2019. We maintained our objection to the TWA application on the 26th May 2020. The attached objection letter sets out our principal areas of concern regarding the potential effects of the TWA application on important wildlife features which are mirrored, and in part amplified, in this response. The comments in our objection letter to the TWA application should also be taken as applying to the ML application. | N/A
Although, further environmental information has been submitted in March, May and July 2020 by the Applicant, only the latter two submissions were specifically submitted to NRW for the Marine Licence application. Therefore, our response to the Planning Inspectorate on the TWA application only includes comments regarding documents in the Applicant’s further information submission from March. Whereas our comments below also refer to the most recent versions of relevant documents. | All documents submitted to the Marine Licence process were submitted to the TWA Inquiry in October 2020. All subsequent documents submitted during the TWA Inquiry are submitted to the Marine Licence process in Feb 2021.
Please know we are continuing to question why the two further submissions are not also being made for the TWA application with the Applicant originally providing one environmental statement for both applications (marine licence and TWA) and therefore any further environmental information should also be to both application processes.
Outline Environmental Mitigation and Monitoring Plan (Revised) - MOR-RHDHV-DOC-0072 (03) | N/A
Whilst we welcome this third version of the outline EMMP and the further detail it contains on the use of trigger points and monitoring requirements, including measures which are now incorporated re the stopping or removal of tidal devices if monitoring indicates adverse effects. We continue to have concerns on a number of aspects.
First, for further legal certainty we think the proposed phased approach needs to be included within the Marine Licence itself. Helpfully this is part of the Applicant’s application and in addition the further detailed required can be added by NRW due to the power to grant Marine Licence applications with conditions due to a need to protect the environment (as set out in section 69(1) Marine and Coastal Access Act 20091). | The phased approach is secured through the Device Deployment Protocol and EMMP (ML Conditions 1 and 40 respectively)
Second, although the further work undertaken on identifying potential monitoring methods has been presented, there is still insufficient information on how the methods will be developed and applied. | The Outline EMMP provides an unprecedented level of detail at the preconsent stage which has not been required of other tidal developments, such as SeaGen and MeyGen. For previous tidal projects the full details of monitoring were developed post consent. The Outline EMMP proposed for Morlais and the associated proposed Marine Licence condition provides security that the monitoring proposals must be agreed with NRW prior to deployment.
Please know that the RSPB fully supports the vital monitoring and research to increase our understanding of how seabirds interact with, and are impacted by, tidal devices. The evidence base gathered if this proposal goes ahead would provide much needed clarity on how and if this technology can be deployed, increasing certainty for developers and investors whilst still ensure the environment is protected. However, due to the necessary monitoring techniques being in their infancy, further developing and testing is required before they can be relied upon. | The Applicant welcomes RSPB's recognition of the important monitoring and research opportunities posed by the project. The EMMP for Morlais includes a suite of measures to monitor seabirds, the details of which must be agreed with NRW in consultation with the Advisory Group prior to construction. Measures such as the proposed colony counts and tracking studies are not new techniques. Other methods which are more novel are associated with monitoring near-field interactions and are being used with initial success at other tidal sites. For example, the APBmer (2020) Review of Potential Collision Between Tidal Stream Devices and Marine Animals shows active sonar has provided initial evidence of near-field evasions and the Enfait (2020) Enabling Future Arrays in Tidal shows successful use of underwater cameras to monitor near-field activity in suitable conditions.
Therefore, as mentioned above, we welcome the inclusion of a Phased approach to the deployment of devices within the OEMMP. However due to many remaining areas of uncertainty, to ensure that this Phased approach adequately addresses the principles of adaptive management enshrined in NRW’s guidance we would like to see the phases tied more directly to monitoring methods and technology that encapsulate both potential population and collision impacts on birds, focusing on razorbills and guillemots. | The EMMP has incorporated NRWs Advice on adaptive management of the risk of collision impacts on protected marine mammal species in Welsh waters from the Morlais Project. The Outline EMMP shows that the phases are tied to the monitoring e.g. Paragraph 39, bullet 2 states "If the results of monitoring of the first phase of deployment indicate that the next phase of deployment could begin without an adverse effect on marine mammals or birds, then the next phase of deployment would be authorised for deployment"
Marine Ornithology Collision Risk Modelling (Version 2) - MOR/RHDHV/DOC/0115 | N/A
We raised concern about calculations presented in the Marine Ornithology Collision Risk Modelling Note and sought clarification on the matter at a meeting with the Applicant on 04/08/20. The Applicant agreed to provide an updated version, and this document, dated 4th September 2020, has been provided. It supersedes document 13_MOR-RHDHV-DOC-0115 as published in March 2020.
Unfortunately this document did not provide sufficient detail on the amended calculations for the RSPB to be able to make a decision as to the robustness of the method used, and as such cannot be relied upon to provide evidence of a reduced impact on the affected species populations. | The full calculations have since been provided to RSPB and discussed through the TWAO process, and have been subject to detailed discussion between the Applicant and RSPB during the Inquiry process. Ultimately, the critical conclusion from these discussions is that RSPB agreed that the scale of impact predicted for the Phase 1 deployment was not significant for the guillemot and razorbill populations at the South Stack and Penlas colonies, as per paragraph 207 of the Menter Môn closing submission: Fourth, there is agreement by all parties that the proposed Phase One of the development will not have a significant effect on guillemot and razorbill361. The relevant modelling note Marine Ornithology Collision Risk Modelling Note362 (the “ornithology modelling note”) predicts minor adverse effects – a low magnitude of impact – on these birds; an assessment from which neither NRW nor RSPB in the end dissented. Footnote 361 states: See NRW’s response at FEI REP004 p. 9 of 23, para A.29; see POE007.1 Dr McCluskie’s Proof of Evidence at para 8.1 and his answers in evidence in chief and XX. Footnote 362 states: MDZ/A31.10.
This updated document also misrepresents the position taken by the RSPB at the meeting on 04/08/2020, stating that the RSPB agreed with the approach taken to amend the collision mortality estimates. The RSPB said that they may agree with the approach if sufficient detail of the working of the calculation were provided. These details have not been provided and so we are unable to agree with the approach. We will continue to engage with the Applicant to get further clarification on this point. | It was not the Applicant's intention to misinterpret the RSPB’s position, this presumably results from a misunderstanding of the discussions had at that meeting. The further details referred to have now been provided to RSPB (as of 26/10/20).
Onshore Ornithology. Response to Chough comments F2.0 PUBLIC - MOR/RHDHV/DOC/0120 | Noted
The Applicant has presented clarification of data, a revision of potential loss of Chough foraging habitat during construction and consideration of functional linkage of land outside the SPA boundary but on which the SPA species are reliant. We note that mitigation for Chough during the breeding season has been revised through the lengthening of the mitigation period (20 March until 31 July). We consider the additional 10 days applied to the mitigation period to be helpful.
In our response letter regarding the further information submitted to the TWA application dated 26 May 2020, we provided comment about chough foraging matters in Terrestrial Ecology Assessment Update (MOR/RHDHV/DOC/0110): | The RSPB confirm in their Proof of Evidence to the Inquiry (available at https://www.dropbox.com/s/sglwakc531ecbri/The%20RSPB%20Updated%20Proof%20of%20Evidence%2023%2011%202020.pdf?dl=0) that they "defer to the expertise within the NRW Advisory Team as to whether this level of detail is sufficient for conducting a robust Habitats Regulations Assessment in relation to the Glannau Ynys Gybi/Holy Island Coast SAC". This position is also cross referenced in paragraph 10, footnote 9 of their closing submission, whilst it was confirmed during cross-examination that the RSPB do not pursue any issue on impact on SPA chough (paragraph 66 of the Menter Mon closing submission).
“We welcome the revised working methods in relation to cloddiau (an important foraging resource for Chough) in 7.1.1, through the application of trenchless methods to avoid direct impact.”
The above measures help address our concerns regarding the Glannau Ynys Gybi / Holy Island Coast SPA. However, some of the land-based works need further clarification to address remaining concerns regarding the cable landfall within the Glannau Ynys Gybi / Holy Island Coast SAC (see below).
Cliff Habitat Design Refinement Note - MOR-RHDHV-DOC-0135 | Noted
There remains to be no indication as to whether the primary landfall option of Horizontal Direct Drilling is possible. A potential landfall route for the secondary option has been identified, that entails pinning cables to the cliff and trenching cables across fields. SAC habitat affected by the secondary option is now calculated to be a permanent loss of 330m2 and a temporary loss of 180m2.
We defer to the NRW advisory team if this level of detail is sufficient for conducting a HRA in relation to the Glannau Ynys Gybi / Holy Island Coast SAC.
Whilst we have endeavoured to respond in full to this consultation process please be aware that key members of our staff are still furloughed and we wish to reserve the right to comment further if necessary. We are also aware that there are other key organisations that are furloughed until the end of October who may wish to engage with the Marine Licence application. | N/A

## RSPB Additional Info
RSPB Additional Information – response to PI 2020-05-26
Feedback | Response
Annex 1 – The RSPB’s detailed comments on Additional Environmental Information forming part of the Environmental Statement submitted as part of the Transport and Works Act Order dated March 2020
Outline Environmental Mitigation and Monitoring Plan (MOR/AEC/DOC/0001)
General Planning Objections
We remain concerned with regard to the content and lack of clarity within the revised Outline Environmental Mitigation and Management Plan (OEMMP) submitted by Menter Môn dated the 25th March 2020. Our initial concerns and objections have not been taken into consideration. Our main objections include: | See below
• The Advisory Group needs to have capacity to amend the OEMMP as well as to oversee the implementation and this is not clear within the document. This application involves the installation of new technology that has not been designed and tested to date and therefore the OEMMP cannot foresee all of the environmental impacts that may arise. The OEMMP therefore needs to be more flexible and comprehensive in nature. | The EMMP and adaptive management plan will be progressed and developed post consent in consultation with NRW (and the Advisory Group) to ensure that effective monitoring is established. A revised outline EMMP (MMC447 MOR-RHDHV-DOC-0072 (09)) is provided with this submission (19th February 2021).
• The OEMMP needs to cover the construction and installation aspects to the development as well as the operational and maintenance processes. Whilst the Construction Environmental Management Plan (CEMP) normally sets out good practice measures, it will not set out the monitoring and mitigation of the construction and installation impacts. This development involves new and multiple different types of technology with different installation methods all with the potential to cause major disruption over a prolonged period which requires careful monitoring and responsive mitigation. | Construction impacts are not considered to be significant to ornithology and therefore it is proposed that the EMMP focusses on impacts from O&M.
• The significant adverse effects set out within the Environmental Statement (ES) are wholly unacceptable given the scale and extent of the impact and therefore we remain opposed to the reference to deploying the maximum installed capacity of the project, without the necessary controls in place through a robust and legally binding OEMMP. | The adaptive management approach will be secured through a consent condition, such that no tidal devices may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (EMMP) is agreed with NRW, supported by an Advisory group of relevant stakeholders. In paragraph 4(iii) of the RSPB Closing submissions to the Inquiry (available at: https://www.dropbox.com/s/htu515jxkkx2xk1/Morlais%20Demonstration%20Zone%20the%20RSPB%20Closing%20Submissions%2011.2.21.pdf?dl=0), the RSPB "acknowledges and accepts that those reported significant effects [from 240MW deployment as reported in the ES] do not take into account the mitigation which is proposed through phasing and the EMMP". The mitigation secured through the EMMP will ensure that the significant effects reported in the ES will not occur.
• The relevant monitoring measures necessary for this type of development as outlined within the OEMMP do not currently exist. A new monitoring method needs to be agreed and trialled in tandem and the deployment of the new technology prior to the deployment of each phase or new technology. | The monitoring methods proposed for marine birds both before and during the first phase of deployment will provide a range of information allowing for reductions in the uncertainty around several parameters key to the estimation of theoretical collision risk and population level impacts. This will enable the refinement of future impact predictions to ensure that decisions on further phases of deployment are based upon the best available information. Several methods are currently under evaluation for suitability for inclusion in the EMMP. Colony counts and productivity surveys of nearby guillemot and razorbill breeding colonies and deployment of Global Positioning Systems (GPS) and Time Depth Recording (TDR) tags on breeding guillemots are two examples which have been used extensively elsewhere. Monitoring of collisions using underwater cameras and sonar is under consideration, though it is acknowledged that technologies that could potentially monitor collisions are currently unproven and therefore the EMMP provides a framework to all the detailed methods to be developed post consent based on the latest available evidence and methods. The requirement for the detailed EMMP to be agreed with NRW prior to deployment of the first phase will be a consent condition. The phased deployment of tidal devices at a magnitude below levels that could result in significant population level effects on seabirds provides an opportunity to provide information which could be used to improve the modelling of collision risk from multiple devices, and further test and develop technologies to determine if a collision event occurred. NRW state in their closing submission: "NRW should also be clear that, so far as monitoring the potential impact of the proposal on birds is concerned (including the risk of diving birds colliding with the development), NRW considers the position to be set out adequately for the purposes of the oEMMP in paragraph 100 of the final draft: i.e. the principle that the collision monitoring should be able to discriminate between marine mammals and other animals, including birds). NRW does not expect the potential impact on birds to be monitored in exactly the same way as the impact on marine mammals. Rather, the extent of monitoring should be appropriate (and proportionate) to the extent of protection afforded by law and policy."
• The models within the OEMMP state that in “the absence of behavioural data the models make conservative estimates”. However, if there is no behavioural data, how do we know that those estimates are indeed conservative? The OEMMP goes onto state that the “conservative assumptions may significantly overestimate the significance of any effects”. It should be noted that in the Environmental Impact Assessment (EIA) and resulting ES there is a need to identify and provide clarity on whether there is no effect, a minor effect, a moderate effect or major effect. In this regard, “may” should not be used within this context, either the projects does or does not have an effect, which should be either minor adverse, moderate adverse or major adverse. In addition, if we do not know what technology is being deployed and how deployment will occur, how can the OEMMP state that the impact has been overestimated? These are questions that need to be addressed in line with EIA requirements before consent can be granted. | In the absence of behavioural data for guillemots and razorbills using the Morlais Development Zone, observations made of the behaviour of these species at other sites have been incorporated into the models, as these represent the best available evidence available to inform the assessment. The phased deployment of tidal devices at a magnitude below levels that could result in significant population level effects on seabirds provides an opportunity to provide information which could be used to improve the modelling for collision risk from multiple devices, and further test and develop technologies to determine if a collision event occurred. The outputs from this monitoring will feed into assessment of impacts for subsequent deployments.
• The OEMMP refers to a framework for monitoring the “potential significant adverse effects” to validate and revise the assessments contained within the ES. The ES is undertaken as an assessment process and therefore cannot be revised post approval. The OEMMP cannot seek to retrospectively revise the ES to establish no significant adverse effect as it suggests. However, mitigation measures that form the output of the OEMMP can potentially reflect newly obtained data. Accordingly monitoring needs to be continual, and mitigation measures may latterly be amended to reflect new information gathered through that monitoring. | The Applicant is not proposing to revise the ES post consent, however in order to undertake adaptive management the impacts will be revisited, incorporating the monitoring data collected during Phase 1, in order to revise the predictions of impacts and inform subsequent deployment phases.
• Paragraph 23, bullet point 1, in relation to Phase 1 does not state any installed capacity, but it does state that “XX installed capacity has no significant impact.” | The OEMMP has been updated (document MOR/RHDHV/DOC/0072(09)). Paragraph 39 explains "Phase 1: Will be installed at a capacity (MW) at which no significant impact is predicted on marine mammals or diving birds using the MDZ. This commitment ensures an initial level of mitigation in place at the start of the EMMP through the limitation of the scale of the development. The scale of the Phase 1 deployment (MW) will be determined by the outcome of modelling of potential collision and encounter risk for marine mammals and diving birds, and associate population modelling, which is in turn dependent upon: • The type of Tidal Energy Converters (TECs) to be installed in the array. • The physical characteristics of the location of the array." NRW, in their closing to the inquiry (available at: https://www.dropbox.com/s/ss3831dg1rszuqg/Morlais%20Closing%20-%20NRW.pdf?dl=0) state in paragraph 37 "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect"
• Paragraph 24 of the OEMMP refers to “several repowering events being predicated” but there is not corresponding mention within the OEMMP of any monitoring or mitigation procedures, let alone what “repowering” consists of. | Repowering is described in Chapter 4 of the ES. The impacts of repowering on Marine Ornithology are assessed in Chapter 11 of the ES.
• Adaptive Management –The OEMMP states that an Adaptive Management approach to the development will be implemented. As previously noted in our original submission we object in principle to the Adaptive Management approach for a development of this size and scale with the significant adverse impacts associated with it. No additional detail on the Adaptive Management process has been provided as part of the new information submitted by Menter Môn and we therefore set out in a separate section below our objection to this approach. | Adaptive management ensures that the project is developed in a Phased approach with a size and scale which is deemed by the Regulator to have acceptable impacts.
• Whilst we welcome within Paragraph 26 the inclusion of a short term precautionary mitigation being proposed through the limitation of an initial deployment to a level where there is “no significant adverse effect as a result of collision with tidal devices is predicted” there is no subsequent mention of what that level is proposed to be. | As above, the OEMMP has been updated (document MOR/RHDHV/DOC/0072(09)). Paragraph 39 explains "Phase 1: Will be installed at a capacity (MW) at which no significant impact is predicted on marine mammals or diving birds using the MDZ. This commitment ensures an initial level of mitigation in place at the start of the EMMP through the limitation of the scale of the development. The scale of the Phase 1 deployment (MW) will be determined by the outcome of modelling of potential collision and encounter risk for marine mammals and diving birds, and associate population modelling, which is in turn dependent upon: • The type of Tidal Energy Converters (TECs) to be installed in the array. • The physical characteristics of the location of the array." NRW state in their closing submission to the inquiry (paragraph 37) "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect"
• Given the unknown impacts and the lack of clarity on the monitoring and mitigation contained within the OEMMP we request that the advisory group has the ability to direct that operations are ceased along with removal of arrays control measure that should be included within Paragraph 37 of the OEMMP. | Section 2.5 of the updated Outline EMMP identifies trigger points and gate review stages at which the Advisory Group would be able to input
• We also have concerns over the setup of an Advisory Group and how it will be able to make any changes required whether it be more mitigation or for operations to stop due to unforeseen impacts. In addition we have concerns about the members and makeup of the Group in terms of balance of interest – it appears that each deployment tenant will be a member; the ultimate decision making process and how conflicting interests on differing topics will be adjudicated; as an Advisory Group what right of recourse is there back to the Order if the applicant doesn’t comply with the decisions of the Group once the Order is formally granted. | The operation of the EMMP is clairifed in the revised EMMP. Agreement of the EMMP with NRW, who have control of the operation of the EMMP (as opposed to the Advisory Group), is a condition of the Marine Licence. The condition also requires that the relevant tidal devices shall be operated in accordance with the approved detailed EMMP.
• We welcome the confirmation that the initial stage of the development will be limited to a level where “no significant impacts on sensitive receptors are predicted”, however we would wish to see the developer commit to limiting all stages of the development to a level where no significant impacts on sensitive receptors are predicted. | The adaptive management approach will be secured through a consent condition, such that no tidal devices may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (EMMP) is agreed with NRW, supported by an Advisory group of relevant stakeholders. Appendix 4 of the OEMMP (MMC447 MOR-RHDHV-DOC-0072 (09)) provides a proposed Marine Licence condition which has been agreed with NRW advisory, as stated in NRW's closing to the Inquiry (paragraph 36(2)) "NRW (advisory) also welcomes the Applicant’s agreement to incorporate its draft wording for the proposed condition in the final draft of the oEMMP, in accordance with the text proposed by the Applicant for the condition in its letter to NRW dated 2 December 2020: see Appendix 4 to the latest draft of the oEMMP"
• We also welcome confirmation that the Advisory Group will identify and agree appropriate monitoring and mitigation measures prior to deployment. However, at present, it is clear that the technology does not exist to adequately monitor the impacts of the proposal. | The OEMMP includes a suite of measures to monitor seabirds, the details of which must be agreed with NRW in consultation with the Advisory Group prior to construction. Measures such as the proposed colony counts and tracking studies are not new techniques. Other methods which are more novel are associated with monitoring near-field interactions and are being used with initial success at other tidal sites. For example, the APBmer (2020) Review of Potential Collision Between Tidal Stream Devices and Marine Animals shows active sonar has provided initial evidence of near-field evasions and the Enfait (2020) Enabling Future Arrays in Tidal shows successful use of underwater cameras to monitor near-field activity in suitable conditions. The Applicant therefore maintains that technology does exist to adequately monitor the impacts of Morlais.
• Overall the OEMMP needs to be legally robust, enforceable, with suitable controls which are necessary, specific, relevant, monitorable, and enforceable throughout the lifetime of the project. | The EMMP will be secured by a consent condition, ensuring it is legally robust and enforceable.
• More detailed objections to the monitoring and modelling aspects of the OEMMP have been provided below by our Conservation Scientist. | See responses below
Marine Ornithology Collision Risk Modelling (MOR/RHDHV/DOC/0115)
Outline Environmental Monitoring and Mitigation Plan (MOR/AEC/DOC/0001
Conservation Science Objections
• The revised collision risk assessment is methodologically flawed and therefore inadequate to inform conclusions of adverse impact. | The Applicant considers that the approach used is valid because each of the designs assessed comprise a single device only, so that the collision risk is directly proportional to the number of devices to be installed (and it is essentially the same calculation as undertaken when calculating the ERM or CRM outputs for multiple devices). This is explained more fully in a revision of the Marine Ornithology Collision Risk Modelling Note (Document MMC361 MOR-RHDHV-DOC-0115). This issue is addressed in the Menter Môn closing submission (availble at https://www.dropbox.com/s/qb5wcdxdai0447z/Menter%20Mon%20Closings%20FINAL.pdf?dl=0), paragraph 216 (bullet point (v)), which sets out the basis on which RSPB's position in this regard is flawed.
• The OEMMP is lacking in detail and fundamental questions remain as to the feasibility of the approaches suggested. Without a firmer delineated methodology, consent should not be granted. | The Applicant maintains that the OEMMP provides sufficient detail at this pre-consent stage and the commitments to developing the required detail post consent are secured through the proposed condition provided in Appendix 4 of the OEMMP (Document MMC447 MOR-RHDHV-DOC-0072 (09)). NRW state in their closing "Insofar as NRW would have preferred the oEMMP to contain further detail on certain aspects, it accepts that these matters can be progressed further if and when the detailed EMMP is discussed in due course".
Marine Ornithology Collision Risk Modelling (MOR/RHDHV/DOC/0115)
The RSPB notes the presentation of revised collision risk estimates for the reduced scale devices. However, the method used to generate these estimates appears to be severely flawed, although little detail is given. The method stated is that there is a calculation of “collisions per MW”, based on the original Collision Risk Modelling (CRM) and Encounter Rate Modelling (ERM) presented in the ES documents, and this is then extrapolated onto a maximum MW from the 0.7 bottlenose dolphin collision scenario. Underpinning this calculation is an assumption of a linear relationship between MW output and mortality. This assumption is wholly unproven and almost certainly incorrect. Both the CRM and the ERM use a series of parameters to input into the model calculation1. These parameters include biological parameters related to the species of bird or mammal, such as dive depth and speed, and physical parameters related to the devices, such as rotor diameter. In a similar manner to the above surface CRM, the model outputs will be sensitive to variation in these parameters, but the greatest sensitivity will arise from the biological parameters 2 3. While clearly there will be some relationship between the turbine parameters and output MW, the nature of this relationship is unclear and would require detailed explanation through an engineering report before becoming acceptable. As such, the RSPB consider that the analysis carried out is wholly inadequate and no conclusions as to scale of impact can be based on it | The revised collision estimates are based on calculating a “collisions per MW” value for each technology under consideration for each species, and multiplying this by the maximum number of MW deployable under the "0.7 bottlenose dolphin scenario". The technology under consideration and its input parameters for the modelling have not changed, and it is only the scale of the initial deployment which has been changed compared to the original modelling presented in the Environmental Statement (ES) Chapter 11, Marine Ornithology, Technical Appendix 11.3. Therefore, the device parameters are constant and there is a linear relationship between the number of MW deployed and the number of collisions predicted for each species. This is as discussed and agreed with RSPB during the meeting on 04/08/2020. This means that this approach produces valid theoretical collision estimates for the 0.7 bottlenose dolphin scenario for seabird species. It is important to recognise that the calculation for both the ERM and the CRM involves estimating the collision risk associated with a single device and then multiplying that by the number of devices to be deployed. Therefore, if all devices for a particular scenario are the same (as is the case for the modelling in question), the relationship between MW output and the calculated collision estimate is clearly linear (e.g. to take a trivial example, if the collision estimate for a 10MW device is 1 bird, then there are 0.1 collisions per MW, and the total collision estimate for a deployment of 10 devices can be obtained either by multiplying the 1 bird per device by 10, or the 0.1 birds per MW by 100). Thus, the existence of the linear relationship is irrefutable. This specific issue is addressed in the Menter Môn closing submission at paragraph 26 (bullet point (v) a.), which sets out the basis on which RSPB's position in this regard is flawed and which was accepted by Dr McCluskie of RSPB during cross-examination, i.e.: Dr McCluskie make three complaints about this modelling (which he accepted is predicated on a worst case approach): a. He complains that there is postulated to be a linear relationship between MW of deployment and impact and this is unproven and unlikely to be correct: but this point is a bad one, as he accepted384, because: (i) there is a linear relationship in the modelling between number of devices and collisions385; and (ii) there is a fixed MW rating output for each type of device so that MW and number of devices is thus fully interchangeable in this respect and the relationship is linear; (Footnote 384 refers to Dr Mccluskie's answers in XX).
Outline Environmental Mitigation and Monitoring Plan (MOR/AEC/DOC/0001)
The RSPB welcome the presentation of the outline plan. However, the monitoring section of the plan is very scant in detail with the onus being placed on an advisory group to provide a more detailed methodology. While the role of an advisory group is to be welcomed, little thought has been put into the fundamental feasibility of the suggested approaches and whether they will be able to provide answers to the fundamental questions inherent in a novel technology. As considerable uncertainty exists around the effects of these devices, it is crucial that the monitoring methods are more clearly delineated, with evidence that they will be effective, before any consent is granted. | The EMMP will be developed post consent based on the latest available evidence and methods. The Applicant is currently engaging experts with regards to monitoring studies which could potentially be deployed at Morlais. This is discussed further in the Summary of Advice Provided to Morlais with Respect to Tagging of Guillemots and Razorbills (document MOR-RHDHV-DOC-0150). The requirement for the detailed EMMP to be agreed with NRW (supported by the EMMP Advisory group) prior to deployment of the first phase will be a consent condition. NRW state in their closing: "NRW should also be clear that, so far as monitoring the potential impact of the proposal on birds is concerned (including the risk of diving birds colliding with the development), NRW considers the position to be set out adequately for the purposes of the oEMMP in paragraph 100 of the final draft: i.e. the principle that the collision monitoring should be able to discriminate between marine mammals and other animals, including birds). NRW does not expect the potential impact on birds to be monitored in exactly the same way as the impact on marine mammals. Rather, the extent of monitoring should be appropriate (and proportionate) to the extent of protection afforded by law and policy."
Colony counts
The OEMMP suggests colony counts as a mean of determining the numbers of birds “active within the colonies of interest”. Such counts are a fundamental component of any monitoring scheme and so the inclusion is to be welcomed. However, a more detailed approach of enhanced monitoring, rather than simple counts, is required to capture any sub-lethal impacts of the devices, such as displacement or changes in prey availability. Enhanced monitoring of seabird productivity and population size based at monitoring plots should be conducted on the key seabird species annually from early April to the end of August. Monitoring should closely follow the JNCC seabird monitoring handbook but be conducted at an increased frequency (i.e. when required multiple visits per week) compared to regular monitoring conducted within the colonies to ensure egg-laying, hatching, fledging and possibly failure dates can be derived from the data as accurately as possible. The enhanced monitoring plan should be drawn up, in consultation with any site wardens following preliminary site visits. These discussions and visits should tailor the monitoring to the specific logistical considerations of each site including topography, location of nests and existing work and monitoring plans. An absolute minimum of two years pre-construction monitoring data is required to capture the natural demographic variability. | Further discussions on the subject of colony counts were held with RSPB during the meeting of 04/08/2020. The Project is broadly supportive of RSPB's suggestions regarding colony counts and productivity estimation, and can commit to developing, in conjunction with RSPB and NRW, a programme of colony counts and productivity monitoring.
As well as ensuring a baseline demographic data set any OEMMP must include an analysis of the power to detect change. This power analysis will determine the sample size and frequency of monitoring required to detect an impact of a given magnitude arising from the deployment of the tidal devices. | The detailed EMMP will be developed post consent and will take account of the power to detect a change as a result of the project.
GPS tagging
Species
Tracking by fitting birds with GPS tags is suggested for “diving birds”, without details provided as to which species will be tagged. We presume this refers to guillemot and razorbill, but it is unclear if Manx shearwater will also be included (they are known to dive to at least 55m4). It is critical that this information is provided as considerations such as capture method, tag type, attachment method, and data retrieval will differ depending on species and thereby understanding whether the approach is justified or not will be species specific | To monitor behaviour at the individual level, it is proposed to tag breeding guillemot and razorbill from the South Stack and Penlas colonies. Preliminary advice from RSPB indicates that approximately 15 individuals of each species could be caught and tagged each year, which would occur during the early chick rearing phase. Two types of logger (or sensors) would be employed; Global Positioning System (GPS), which measure the spatial location of the bird, and time depth recorders (TDR) tags, which provide data on diving behaviour (e.g. dive duration and depths). These may be deployed on the birds as two separate loggers or as a single device with two sensors, with decisions on such detailed aspects being made via the EMMP according to the most suitable technology available nearer to the onset of monitoring. It should be noted that contrary to the RSPB's statement on this, integrated tags with both GPS and TDR functions are available (as subsequently recognised in Dr McCluskie's Rebuttal Proof (paragraph 15)). Birds must be caught in order for tags to be fitted. The tags would generally be designed to collect data for a period of several days, after which they would fall off (unless birds are re-caught to retreive the tags - see below). Data would be captured by a remote base station installed at the colony, provided this approach is demonstrated to give suitable data and provided it is feasible at these colonies (requiring line of sight to the nest of the tagged birds to enable download). Alternatively, tagged birds would be re-captured after a number of days to retrieve tags for the purposes of downloading data. Again, contrary to what is stated by RSPB, remote download is feasible for loggers which record dive behaviour data and such devices are currently being used on guillemots and razorbills in another monitoring programme in the UK (again as subsequently recognised in Dr McCluskie's Rebuttal Proof (paragraph 16)). Studies of the foraging behaviour of both guillemot and razorbill are being undertaken in other projects involving the combined use of GPS and TDR devices, and with automated data download incorporated. However, it is recognised that this element is still novel technology, with the success of these systems still to be fully established, and it may be necessary to employ the more well established approaches of re-capturing birds to retreive tags for data download. Further details of the success of using remote download methods for such work will be obtained before finalising the tagging methods. Tagging will be undertaken to monitor the movements and foraging ranges of breeding guillemot and razorbill from the South Stack and Penlas colonies, and to provide site-specific information on the dive behaviour of these species. Contrary to what is stated by RSPB, the tagging work does not aim to monitor collisions with devices (which RSPB correctly state is not feasible by this means). More recent versions of the oEMMP are clear on this point. As noted by RSPB, data collection from tagged birds will be restricted to the chick-rearing period, which may not be representative of the full breeding season. However, adult birds are having to 'work hardest' and undertake more foraging trips at this stage (as they are provisioning young), whilst their ranges are also most constrained at this time so that it is likely to be a period of heavy reliance upon the Project site. Therefore, the value of collecting such data during chick-rearing is high. It is also the case that consideration will be given to assessing possible effects of catching and tagging on the monitored birds. The Project team have recently held discussions with key staff on the SEACAMS project, who have successfully tagged guillemots at Puffin Island with GPS tags and accelerometers (which record dive behaviour). Further discussions are planned to ensure that all available options for the EMMP are thoroughly explored to enable the production of a high quality evidence base by the monitoring programme. The issues surrounding the proposed tagging work were discussed during the Inquiry, with paragraphs 234 to 236 of the Menter Môn closing submission outlining the Applicant's position in relation to the various points RSPB have raised on this matter. It is not the intention to include Manx shearwater in the EMMP at this time. The reason for this is that the MDZ does not make up a substantial proportion of the foraging grounds for this species, as it does not breed at/near South Stack, and significant effects have not been predicted by the ES or HRA. Paragraph 10, footnote 9 of the RSPB Closing Submissions states "the RSPB had sought additional information in respect of Manx shearwater and it was content that impacts were not of concern for that species".
Tag type
The data derived from these studies will provide “location, height, depth, speed and acceleration.” However, only the first of these, location, is obtainable from GPS tags (flight height can be modelled from GPS data to some extent using a Baysian approach5, but this will not provide the location specific data required for monitoring). The rationale also claims that other relevant parameters “such as dive depths and durations” will be obtained. These parameters are also not obtainable from GPS tags.
It is possible to obtain these data from other additional devices that can be used in addition to GPS tags, for example time depth recorders (TDR) or accelerometers. However, in the case of TDRs there are currently no integrated tags that can do both GPS and TDR functions, and TDR tags require recapturing of the birds6, which has implications for both data retrieval and capture methods. Accelerometers, which will provide accurate quantification of movement, can be integrated into GPS tags and such devises have been fitted to both razorbill and guillemot7, however there it is still unclear whether such methods will provide the data required for a comprehensive monitoring scheme, in particular in relation to data retrieval, capture methods and the limited period over which tracking can be carried out.
Capture Methods
All tagging studies require capture of the individual being tagged. As such, consideration is needed in determining capture method to minimise the potential negative impacts of the capture on the bird being studied, both for ethical reasons and to prevent altering the behaviour of the study bird. It is also crucial to consider the safety of the people capturing the birds. These considerations are especially pertinent with cliff nesting species such as razorbill and guillemot, as the risks of injury or causing nest failure are high. Before any work is carried out it is of course important that a feasibility study is carried out, to determine the accessibility and safety of catching (and potentially recapturing) the birds as this will be very site specific. Currently the OEMMP contains no such requirement and at the very least it should, although preferably the feasibility study should be carried out and feed into the OEMMP rather than leaving its important results for later especially if some methods are not feasible and alternatives requires – delaying the start of the pre-construction monitoring .
Data retrieval
No detail has been provided in the OEMMP as to how the data collected by the tags will be retrieved. Essentially there are two methods, in situ or remote downloading. In situ retrieval requires recapture of the bird and removal of the tags, while remote retrieval can be via, for example, satellite, GSM network or using a base station. Satellite and GSM tags are currently too heavy to be used on auk species, including guillemot and razorbill, so the only suitable methods for data retrieval are by using a base station or by recapturing the bird. Currently no TDR tags are available that allow for remote download. Careful, site specific consideration is required as recapture carries similar risks to capture, with the added complication that a bird is much harder to recapture than it is to capture. The use of a base station requires knowledge of the local topography as the station needs to be located in line of sight of the birds’ nest in order that data can be downloaded while the bird is on the nest. Clearly such considerations must be made before the monitoring plan can be finalised. And as mentioned above we are concerned that this information is not currently available.
Timing of study
Currently for razorbill and guillemot, capture methods are largely restricted to a narrow window in the breeding season, early to mid chick-rearing period. Capture of these species should not be undertaken during incubation because of the risk of dislodging the egg. Late chick-rearing period should also be avoided because the chicks are mobile and can potentially move away from the nest site and be at risk as a result. Such phenological constraints mean that any data collected cannot be representative of the whole year and will not include periods when the birds are vulnerable, such as for razorbill and guillemot, post moult. The OEMMP should account for these limitations and explore any means by which they can be overcome.
Collisions
The OEMMP lists collision of diving birds with tidal devices as one of the indicators to form part of the monitoring scheme (also not listed in table 2-1) examined via tagging. However, there are no suitable tags available that will provide this information. The reason for this is that, as noted above, data from the tags needs to be downloaded and it is impossible to do this unless the tags itself is retrieved from the collision victim. As the only method of remote downloading suitable for these species requires the bird to return to the colony, it is impossible for a fatal collision to be recorded. For non-lethal encounters, the bird may abandon the breeding attempt, in which case it also may not return to the colony. It should be noted, therefore, that there is no means of recording collision of diving birds with tidal devices included in the OEMMP, and as detailed in our previous written submission, there is little practical chance of the development of device mounted sensor capable of recording bird collisions.
Baseline
The OEMMP suggest that tracking data will be used to monitor any “change in use of tidal device deployment area pre and post installation”. However, the outline schedule of OEMMP tasks shows that the monitoring work will only commence after construction has begun, so it is impossible for any change in behaviour due to the presence of the tidal devices to be described. As mentioned above, an absolute minimum of two years pre-construction monitoring data is required to capture the natural spatial variability in at sea distribution. Such variability can arise as a result of, for example fluctuations in prey density, and so a robust baseline is needed in order to disentangle such biological stochasticity from the effects of the devices. | Noted, monitoring methods will be progressed post-consent in consultation with NRW and RSPB.
As well as ensuring a baseline spatial data set any OEMMP must include an analysis of the power to detect change. This power analysis will determine the sample size and frequency required to detect an impact of a given magnitude arising from the deployment of the tidal devices | The detailed EMMP will be developed post consent. The detailed methodology requries the final design of the phased deployment.
General Objections to Adaptive Management
The RSPB is concerned about the proposed approach to adaptive management as a way of consenting a large-scale project in the face of such high levels of uncertainty about its impact on seabirds. | A phased approach to installation of devices, with a smaller initial deployment to manage impacts to marine mammals and birds has been introduced. This will be secured by a condition which requires the detailed EMMP to be agreed with NRW in consultation with an Advisory Group, including RSPB. In relation to the potential impacts from the Phase 1 of deployment, all parties (including RSPB) agree that this will not have a significant effect on the guillemot and razorbill populations. This was established at Inquiry, as per paragraph 207 of the Menter Môn closing submission: Fourth, there is agreement by all parties that the proposed Phase One of the development will not have a significant effect on guillemot and razorbill361. Footnote 361 states: See NRW’s response at FEI REP004 p. 9 of 23, para A.29; see POE007.1 Dr McCluskie’s Proof of Evidence at para 8.1 and his answers in evidence in chief and XX.
We question whether it is appropriate to apply adaptive management to such a large ‘project design envelope’ over such a long time period and involving multiple phases and whether such an approach enables a realistic environmental assessment of the full deployment of the scheme. | Adaptive management provides a greater level of control to NRW and relevant stakeholders such as RSPB, whereby the monitoring and mitigation measures can be tailored to the final design of each deployment and subsequent deployments are reliant on suitable evidence from monitoring of the initial phase. NRW state in their closing to the Inquiry "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect"
We also question whether the application meets the letter and spirit of NRW’s guidance on adaptive management (https://naturalresources.wales/guidance-and-advice/business-sectors/marine/using-adaptive-management-for-marine-developments/?lang=en ). | NRW guidance states the following which is exactly the proposed purpose of adaptive management of Morlais: - "adaptive management can enable deployments by helping reduce risks associated with scientific uncertainty. It can also increase our understanding of development effects on the environment." - "It is a structured, iterative approach to environmental assessment, allowing the management of a project to be adapted based on learning once the development has been installed or constructed."
In passing, please note that we think that the NRW guidance is insufficiently detailed and requires further development to provide a robust basis for stakeholders to engage with the process. The guidance needs to better reflect the principles of the Sustainable Management of Natural Resources (SMNR) which NRW is required to apply under the Environment (Wales) Act 2016, including (a) manage adaptively, by planning, monitoring, reviewing and, where appropriate, changing action; (e) take account of all relevant evidence and gather evidence in respect of uncertainties; and (h) take action to prevent significant damage to ecosystems. As the Welsh Government has stated in its recent consultation on Environmental Principles and Governance in Wales post EU Exit, the SMNR principles are intended to encapsulate, in an operational way, the precautionary principle (as well as it currently being relevant for any consideration of EIA mitigation that may be required). | Comment for NRW not the Applicant.
The principle in para 306 of the Wales National Marine Plan needs to be interpreted and translated into guidance. This states that a Deploy and Monitor approach can facilitate the use of a marine area by consenting novel activities on a smaller scale initially, to enable their careful assessment prior to more widespread introduction. We suggest that applying this principle would involve a different consenting approach to that being proposed for the Marine Demonstration Zone by limiting the initial consent to a smaller scale demonstration project. | The adaptive management approach will be secured through a consent condition, such that no tidal devices may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (EMMP) is agreed with NRW, supported by an Advisory group of relevant stakeholders. Therefore the proposed approach is compliant with the NRW guidance.
Referring to NRW guidance (selected extracts below as bullet points in bold type followed by our comments): | N/A
• NRW guidance states that ‘the aim of adaptive management must be to avoid unacceptable environmental effects’. | The draft condition states "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP) the intention of which is to prevent injury marine mammals and diving birds in the operation of those devices, and which is in accordance with the requirements of the Outline Environmental Management and Monitoring Plan (OEMMP), and which incorporates the following (insofar as relevant to that activity or phase of activity) has been submitted to and approved in writing by NRW"
• NRW guidance states that adaptive management is not always the right approach. ‘Where the realistic risk of environmental impacts remain high and we don’t know how successful adaptive management will be, consents may be refused.’ | Paragraph 30 of the OEMMP (document MOR/RHDHV/DOC/0072(03)) shows that Phase 1 will be installed at a capacity (MW) at which no significant impact is predicted on marine mammals or diving birds using the MDZ. All phases of deployment will be subject to the proposed licence condition which states "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW"
We believe the evidence is insufficient to conclude that the impact on seabirds of a full deployment of a 240MW consent is manageable through adaptive management. | This is the purpose of the adaptive management approach, in that the full 240MW deployment will only be possible once sufficient evidence is available to allow NRW to agree the DEMMP for subsequent phases based on the information obtained during Phase 1. NRW state in their closing to the Inquiry "Given the Applicant’s constructive acceptance of NRW’s proposals for strengthening the adaptive management mechanisms in the oEMMP, NRW is able to advise the decision - maker that there would be no such adverse effect"
The applicant states that assuming a 95% avoidance rate (for population modelling) there would be a major adverse effect for breeding guillemot and razorbill at South Stack on full deployment. The main basis on which a minor adverse effect is claimed for full deployment is that ‘monitoring enables a higher avoidance rate to be applied’, we presume this means to subsequent phases (Table 11.34 in Morlais ES Chapter 11). This is a wholly untested assumption and there is no certainty that it will be found to apply – it should therefore be discounted as a ‘mitigation measure’. Please refer to our previous response to the TWAO regarding avoidance rates. | The assumption is based on the requirement of the condition which ensures "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW." Therefore the full 240MW deployment will only be possible once sufficient evidence is available to allow NRW to agree the DEMMP for subsequent phases based on the information obtained during Phase 1.
We suggest that this is a case where adaptive management at the scale envisaged is not the right approach because the realistic risk of impact to seabirds remains high. | The realistic risk of impact to seabirds of Phase 1 is low as presented in the Collision risk modelling (Document MOR-RHDHV-DOC-0115). The full 240MW deployment will only be possible once sufficient evidence is available to allow NRW to agree the DEMMP for subsequent phases based on the information obtained during Phase 1. In relation to the potential impacts from the Phase 1 of deployment, all parties (including RSPB) agree that this will not have a significant effect on the guillemot and razorbill populations. This was established at Inquiry, as per paragraph 207 of the Menter Môn closing submission: Fourth, there is agreement by all parties that the proposed Phase One of the development will not have a significant effect on guillemot and razorbill361. Footnote 361 states: See NRW’s response at FEI REP004 p. 9 of 23, para A.29; see POE007.1 Dr McCluskie’s Proof of Evidence at para 8.1 and his answers in evidence in chief and XX.
Modelling needs to be undertaken and presented for smaller scale deployments to identify a level of deployment that would not have a significant impact on seabirds. | Collision risk modelling for the smaller Phase 1 is provided in Document MOR-RHDHV-DOC-0115
• NRW guidance states use feasible mitigation measures that have a high chance of success. | The OEMMP provides feasible mitigation, in that no tidal devices (for any phase) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (EMMP) is agreed with NRW, supported by an Advisory group of relevant stakeholders. This phased approach will mitigate impacts on seabirds and marine mammals.
• A project can only be approved if the appropriate mitigation for the realistic worst-case scenario can be secured and is feasible with a high chance of success. | A draft condition has been proposed by the Applicant to ensure the commitment to mitigation through the framework of the EMMP is secured. No tidal device(s) may be constructed or repowered until a DEMMP has been approved in writing by NRW.
The proposed ‘mitigation measure’ is not feasible as there is no certainty that a higher avoidance rate will be found to apply. As noted in our previous TWAO response we are also concerned about the lack of detail about how the proposed collision avoidance monitoring scheme would work and indeed considerable uncertainty remains as to whether such monitoring is even possible given current technology. There is no precedent for an avian monitoring scheme being successfully carried out on similar devices. For any proposed measures to be considered effective mitigation, they must be evidence based so there is a high confidence they will be successful. The phasing, monitoring and mitigation scheme must be evidence based, clearly presented, agreed, legally binding and secured within the Order. | The proposed condition ensures "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW." Therefore the full 240MW deployment will only be possible once sufficient evidence is available to allow NRW to agree the DEMMP for subsequent phases based on the information obtained during Phase 1. Through this commitment there is sufficient certainty that the mitigation must be delivered. The Applicant notes RSPB's comment regarding securing the condition in the Order, as this consultation is related to the Marine Licence the Applicant would note that a draft Marine Licence condition has been proposed as shown in Appendix 4 of the OEMMP. This is agreed with NRW Adisory as stated in their closing "NRW (advisory) also welcomes the Applicant’s agree ment to incorporate its draft wording for the proposed condition in the final draft of the oEMMP, in accordance with the text proposed by the Applicant for the condition in its letter to NRW dated 2 December 2020: see Appendix 4 to the latest draft of the oEMMP"
No feasible mitigation measures are offered in the case of the applicant’s ‘worst case’ scenario being confirmed by monitoring of an initial 12MW deployment, and no feasible means of monitoring have been presented. | The EMMP will be developed post consent based on the latest available evidence and methods. The Applicant has engaged with experts with regards to monitoring studies which could potentially be deployed at Morlais. This is discussed further in the Summary of Advice Provided to Morlais with Respect to Tagging of Guillemots and Razorbills (document MOR-RHDHV-DOC-0150). The requirement for the detailed EMMP to be agreed with NRW (supported by the EMMP Advisory group) prior to deployment will be a consent condition which ensures "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW." Through this commitment there is sufficient certainty that the mitigation and monitoring must be delivered.
• NRW guidance states that an applicant should clearly define the required adaptive management in a strategy or plan - for example an Adaptive Environmental Management Plan (AEMP) - that you'll need to agree between the relevant parties. This can include us and other regulators, advisors and other stakeholders. | As above, the adaptive management approach will be secured through a consent condition, such that no tidal devices may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (EMMP) is agreed with NRW, supported by an Advisory group of relevant stakeholders. An assessment of a much smaller first phase has been submitted (Marine Ornithology Collision Risk Modelling, document MOR/RHDHV/DOC/0115) which represents a highly precautionary approach to adaptive management. The urgent progression of this application is critical to the success of the project and the delivery of its benefits to local communities, the economy and development of renewable energy.
The applicant has provided as part of their TWAO and ML application, a revised document titled Outline Environmental Mitigation and Monitoring Plan (MOR/AEC/DOC/0001). We have major reservations about the lack of detail and approach taken as set out above. We suggest that NRW and interested stakeholders including the RSPB need to see much more detail at the pre-consent stage. We note that NRW guidance says that an AEMP should be agreed ‘early in the consenting process’. If the Inspectorate and Ministers are to progress the application, then a detailed AEMP should be provided and agreed with relevant parties. | As above, the EMMP will be developed post consent based on the latest available evidence and methods. The Applicant is currently engaging experts with regards to monitoring studies which could potentially be deployed at Morlais. This is discussed further in the Summary of Advice Provided to Morlais with Respect to Tagging of Guillemots and Razorbills (document MOR-RHDHV-DOC-0150). The requirement for the detailed EMMP to be agreed with NRW (supported by the EMMP Advisory group) prior to deployment will be a consent condition which ensures "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW." Through this commitment there is sufficient certainty that the mitigation and monitoring must be delivered in accordance with similar approaches that have been taken in the consenting of offshore wind farms.
We therefore believe that it is inappropriate to consent the full deployment and operation of up to 620 devices and that this is not an appropriate and precautionary application of adaptive management principles. | The proposed condition ensures "No tidal device(s) may be constructed or repowered until a Detailed Environmental Management and Monitoring Plan (DEMMP).... has been submitted to and approved in writing by NRW." Therefore the full 240MW deployment will only be possible once sufficient evidence is available to allow NRW to agree the DEMMP for subsequent phases based on the information obtained during Phase 1. Through this commitment there is sufficient certainty that the mitigation must be delivered.
We are also concerned that this TWAO application is being progressed ahead of the work of the Strategic Consenting Advisory Group established at the request of Welsh Government and on which NRW and the RSPB is represented. | The urgent progression of this application is critical to the success of the project and the delivery of its benefits to local communities, the economy and development of renewable energy.
Welsh National Marine Plan Comparison Note (MOR/RHDHV/DOC/0128)
Since initial submission of the TWAO application the Wales National Marine Plan (WNMP) has been formally amended and adopted. This is a statutory document. Menter Môn have acknowledged that there are some minor alterations to policies within the WNMP, however the applicant’s Marine Policy Review states that there is no new information or alterations needed to their existing submission. | See below
We believe Menter Môn should provide further information with regard to how the development complies with GEN01 and GEN02 in conforming with the principles of sustainable development in so far as the development does no harm for future generations. Given the worst case scenario shows the potential loss of 521 guillemots and 259 razorbills per annum from the sea bird colony it is therefore clear that the development does not comply with the ethos of these policies. | Gen_01 states "There is a presumption in favour of the sustainable development of the plan area in order to contribute to Wales’ well-being goals." The project benefit towards well-being is discussed in ES Chapter 2, Policy and Legisaltion. Gen_02 states "Relevant public authorities should take a proportionate, risk-based approach to application of relevant marine planning policies in decision making". By adopting an adaptive management approach, the project is taking a proportionate and risk based approach. In paragraph 4(iii) of the RSPB Closing submissions to the Inquiry, the RSPB "acknowledges and accepts that those reported significant effects [from 240MW deployment as reported in the ES] do not take into account the mitigation which is proposed through phasing and the EMMP". The mitigation secured through the EMMP will ensure that the worst case effects described in the RSPB's comment will not occur.
With regard to GEN02 we believe that further work is required to comply with the precautionary principle outlined. It is clear that a risked based approach needs to be taken that therefore requires that the detail of the mitigation and monitoring of impacts to be set out more clearly and comprehensively. i.e in a clearly defined Adaptive Environmental Management Plan. | As above, the policy refers to a proportionate and risk based approach which is being adopted by the use of an adaptive management approach.
Navigation Risk Assessment - Morlais Tidal Demonstration (18UK1479-RN-MM-NRA-20_03)
The ES does not appear to have considered the displacement of recreational craft from the Morlais Demonstration Zone (MDZ). Small recreational craft will be required to navigate around the western or eastern boundaries of the MDZ. | ES Chapter 15 Shipping and Navigation (MOR/RHDHV/DOC/0029(2)) and NRA Addendum (MOR/RHDHV/APP/0030(3)) demonstrates that approximately 90% of existing vessel traffic already uses what will become the Eastern Inshore Route. Therefore there is unlikely to be significant change to recreational craft from the Morlais Demonstration Zone (MDZ) that could lead to a significant impacts on marine mammals or ornithology.
The concentration of recreational craft in the Western Offshore and Eastern Inshore Routes has the potential to cause additional disturbance to marine wildlife (seabirds and marine mammals) and could potentially displace marine wildlife into the MDZ. This does not appear to have been factored into the Marine Ornithology Collision Risk Modelling and Marine Mammal Collision Risk Modelling.
Furthermore, there is potential for increased disturbance to the seabird colony and shoreline areas used by marine mammals through the concentration of small craft in the Eastern Inshore Route.
Review of Onshore Ornithology Response to Comments on Chough (MOR/RHDHV/DOC/0120)
This document was submitted in response to NRW’s request for further information on Chough and Special Protection Area (SPA) matters. The applicant has presented clarification of data, a revision of potential loss of Chough foraging habitat during construction and consideration of functional linkage of land outside the SPA boundary. We note that mitigation for Chough during the breeding season has been revised through the lengthening of the mitigation period (20 March until 31 July). | Agreed
Terrestrial Ecology Assessment Update (MOR/RHDHV/DOC/0110)
The applicant has presented additional information however there remains a high level of uncertainty in relation to the impact of the cable landfall owing to an indecision on which working methods will be applied. Furthermore, the refinement of onshore works in relation to secondary landfall option is reliant upon the results of a National Vegetation Classification (NVC) survey which is yet to be conducted. | Further Environmental Information has been submitted in July 2020 (MOR-BSG-DOC-0001), which includes the results of the survey and further refinement of the landfall works to mitigate impacts
The proposed micro sighting and adoption of narrower working corridors for the secondary landfall option is welcomed but the route remains undetermined until NVC surveys are undertaken. Unfortunately, the extent of the NVC survey study area is not clear as to whether it extends into Glanau Ynys Gybi/Holy Island Coast SSSI, SPA, SAC and if it impinges upon the RSPB Reserve? In addition, it is not clear if this year’s survey work is the same as or additional to the preconstruction NVC survey listed in section 7.1. of the update. We request early sight of amendments of details and extent of any overlap with the RSPB reserve in light of completed NVC surveys. | As above
We welcome the revised working methods in relation to cloddiau (an important foraging resource for Chough) in 7.1.1, through the application of trenchless methods to avoid direct impact. We acknowledge the addition of pre-construction checks for barn owls will include mature trees. | Agreed
Supplementary Tourism and Recreation Assessment (MOR/BAU/DOC/0001)
Whilst we are unable to provide a detailed analysis at present to this document due staff being on furlough, we set out below a number of our initial objections to the Tourism Assessment. | N/A
• The methodology described Page 10 is weak. The assumed data is basic with incorrect analysis. There are many influencing factors to the baseline data. | Given limited data availability, the triangulation approach gives a robust method for identifying a baseline and monitoring the impact, if any, of the tidal energy project on tourism and recreation activities at Holy Island.
• Monitoring is weak. Selected and interviewed business included RSPB however this process was not formal at the outset, there was no set questionnaire with guidance to complete. No questions about the impact Morlais may have on our business. The RSPB sent through the requested information in early April and it is unfortunate that it was not able to be incorporated within the new documents. A suggested standard is to use STEAM modelling which is commonly used to analyse tourism. | Future analysis will consider utilising STEAm.
• Case studies although it is not possible to find a comparable project, new case studies are weak. Llandudno is an urbanised area, Pembrokeshire case study is situated 15km plus from the coast line. | Given it is not possible to find comparable project, case studies of similar activities have been considered to infer the likely impact the development will have on tourism and recreation activities.
• Lack of data regarding knowledge of tourism, page 28.29. The statements regarding introducing new Energy tourism do not consider the already growing ‘wildlife tourism’ which is a known. It is not known as to whether the new tourism would supplement or replace the existing. Collecting data via questionnaires from visitors at key locations at different times of years as Wylfa Newydd did would assist with a correct analysis. | Collecting data via questionnaires from visitors at key locations at different times of the year will be considered as part of the baseline development process and monitoring.
• Monitoring section 10, pg37 does not show the impact on individual business. The data collection is weak, overall labour in tourism, counters on a footpath and interviews. A more robust model such a STEAM would give a better analysis of the impacts on the individual businesses as well as the wider community. Reflecting more accurately the impact on supply chain. | Future analysis will consider utilising STEAm.

## FEI_ML011 RYA
FEI_ML011 ORML1938 – Consultation Response, RYA
Feedback | Response
Following review of the Further Environmental Information (FEI), the Royal Yachting Association (RYA)1, on behalf of our membership, continues to object to Marine Licence application ORML 1938 | We note that the comments received from the RYA predate the NRA Addendum and the Amended ES Chapter on Navigation and Shipping, two documents which we believe address a number of the points raised by the RYA. The development has also been the subject of a Public Inquiry in relation to the TWAO application which has further clarified a number of points. Therefore, we have not supplied a line by line response to the RYA's comments as things have moved on considerably and we believe many of the points have been addressed. However, we have supplied bief notes on the main items they have listed. Furthermore it is worth noting that progress has been made with the RYA who, through their TWAO Public Inquiry Closing, advised that of four main concerns three had "fallen away" namely: 1. The design options had not been finalised, making it impossible to assess the full impact of the project on recreational boating activity; 2. The Navigation Risk Assessment (and its Addendum) and the Interactive Boundaries Assessment did not comply with MGN543; 3. The Navigation Risk Assessment (and its Addendum) and Interactive Boundaries Assessment apparently relied exclusively on AIS and radar data to provide information about boating activity in the vicinity, which risked overlooking the significant proportion of recreational boats which do not carry AIS and offer a small radar silhouette;
In summary, the FEI has failed to address the concerns of the RYA, and our objection continues for the following reasons: | Responses below:
1. The order application Environmental Statement and Navigation Risk Assessment fail to | The two full NRAs completed by the applicant followed the FSA methodology approved by the IMO, and are considered compliant with MGN 543 as agreed by the MCA.
consider all possible maritime safety impacts to recreational craft;
2. The use of Automatic Identification System (AIS) data to advise the Navigation Risk Assessment | With respect to the accusation that the applicant has not included data covering the peak recreational period: The MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements." With regard to the question of the timing of data acquisition, consultation with recreational stakeholders indicated that July and August through to the August Bank Holiday were the busiest period for users. The 2017 summer survey commenced on the August Bank Holiday weekend and so is representative of this busy period. With respect to the accusation that the applicant has not considered non-AIS equipped recreational craft: Once again we would highlight that the MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements." 28 days of surveys including AIS, RADAR and Visual surveys were completed between August and September 2017 and in April 2019. Through the course of the TWAO process it was firmly established that visual surveys were completed and the results incorporated into the NRAA and this was acknowledged. In the RYA's Closings for the TWAO Public Inquiry, in relation to visual data they have stated: "In January 2021, during the hiatus in the inquiry, the applicant provided us with evidence that a visual survey of vessel traffic had been carried out by the applicant’s contractor during August and September 2017." They still express concerns about hwo this data was used in the NRAA which we are happy to address but they do go on to say "Nevertheless, we do now acknowledge that a visual survey was carried out."
and Interactive Boundary Assessment did not fully include the peak recreational period and
does not appear to consider non AIS equipped recreational craft;
3. The Navigation Risk Assessment on which the application is based has failed to follow the | The MCA have agreed in the statement of common ground with the applicant that the survey data goes "over and above MGN 543 requirements. "In the RYA's Closings for the TWAO Public Inquiry in relation to their objection: "The Navigation Risk Assessment (and its Addendum) and the Interactive Boundaries Assessment did not comply with MGN543;" the RYA have stated that "Similarly, the MCA has since confirmed that, in its view, the applicant had done all that was required of it under MGN543 so our objection in this regard has also fallen away."
guidance of Maritime Guidance Note (MGN 543): Safety of Navigation: Offshore Renewable
Energy Installations (OREIs) - Guidance on UK Navigational Practice, Safety and Emergency
Response leading to an incomplete and inaccurate Navigation Risk Assessment;
4. Assessment of recreation and tourism activity fails to fully analyse the implications of the MDZ to recreational boating, and; | Chapter 25 of the ES addresses the socio economic impacts of the development. In particular paragraph Section 25.4.8 looks at Recreation and looks at the national, regional and local level. At the regional level, it refers to both kayaking and sailing as a popular regional activities across North Wales (see para. 131). At the local level, sailing is outlined at para. 139, and kayaking at para. 142. Para. 139 also cross refers to the shipping and navigation chapter of the ES , which includes a significant amount of detail, both there and in the NRA and NRAA on use by boats. That ES was scoped with PINS, which did ask for more information and tourism and recreation but not boating specifically. The applicant also undertook a Supplementary Tourism and Recreation Assessment between January and March 2020 focussed on tourism and recreation (which included a survey of both land-based and marine-based enterprises). Finally the applicant has committed to monitor socio-economic impacts (both land-based and marine-based) of the development and mitigative if they are negative.
See further points below
5. The Rochdale Envelope/ Project Design Envelope approach has not been applied in keeping with guidance. | The Rochdale Envelope or PDE approach taken by the applicant was examined in detail in the TWAO Public Inquiry and the RYA did not challenge the evidence given on this topic. The ‘Rochdale Envelope’ approach is employed where the nature of the Proposed Development means that some details of the whole project have not been confirmed (for instance the precise number and/or location of structures) when the application is submitted, and flexibility is sought to address uncertainty. To allow for future developments and innovations in the type and nature of tidal energy devices that may be deployed across the site the NRA and ES considered a “worst case” scenario where any type of device, floating, subsurface of seabed mounted could be deployed across any part of the development site. Note that the proposed ML Conditions would require an array specific NRA to be undertaken before any new deployment which would then necessarily consider the detailed parameters of the proposed array in the specific location, and also with respect to any previously installed arrays. In additon the project is committed to updating the overarching site NRA every two years to monitor any changing circumstances.
It is noted that NRWL specifically asked for clairifccation on the socioeconomic representations. For this reason the main socio-economic points raised by RYA are addressed below:
i. We note that the supplementary document uses a two-step methodology: Step 1 involves interviews to “provide context to the economic analysis”. Whilst the assessment identified the presence of clubs, racing and nearshore boating activity, it did not undertake interviews with RYA affiliated clubs. | See p.293(iv) of Morlais closings "The RYA sought to criticise the number of organisations contacted for interview, in particular suggesting boating and sailing clubs had not been contacted. Our responses are: a. there were attempts to contact other businesses (including, for example, sea kayaking UK) but they did not respond. b. as you heard from Dr Jones – accommodation and food are the main drivers of tourism related economic activity in the area, and so the focus is on ensuring that is properly represented. c. The RYA prevented Menter Môn from engaging directly with boat clubs."
ii. The clubs, and their membership, are significant recreational providers and economic drivers to the area. | See p.283, p.290(ii) and p.290 (iii) of Morlais closings: (iii) "Turning, then, to socio-economic matters, the majority of the time at the socioeconomic RT was taken up with matters in issue between Menter Môn and SCC/RYA. This largely focused on the economic impacts on tourism reflected through alleged impacts on marine related activity. We are going to deal with that below and the complaints they make, but it should be noted at the outset that this is a small section both of local tourism and the local economy, as Ms Wong for SCC accepted when you put that to her. " "A concern has been raised regarding the extent to which water sports recreational amenity users feature in that baseline. We refer you in particular to paras. 25.4.8. That looks at the national, regional and local level. At the regional level, it refers to both kayaking and sailing as a popular regional activities across North Wales (see para. 131). At the local level, sailing is outlined at para. 139, and kayaking at para. 142. The consideration at para. 139 also cross refers to the shipping and navigation chapter of the ES , where you will find a significant amount of detail, both there and in the NRA and NRAA on use by boats. That ES was scoped with PINS, which did ask for more information and tourism and recreation but not boating specifically. " "Mr Hill further queried the extent to which long distance cruising from Scotland Northern Ireland, the Isle of Man and the Republic of Ireland featured in the baseline. Again, to the extent these contribute to the local economy through matters such as job creation and visitor spend, that is caught. "
iii. The Seabed User and Developer Group (SUDG)indicate that maritime sectors “do not conform well to Standard Industrial Classification (SIC)definitions used in government economic statistics. Typically it is found that the SIC codes do not adequately match the sector specific activities (i.e. they encompass a broader set or only partial coverage) and/ or they do not provide a distinction between marine and terrestrial activities of a similar nature.” | See p.293(iii) of Morlais closings: "(iii) A question was raised by RYA about the use of NOMIS data. The RYA suggested that the Seabed User and Developer Group considered that the use of Standard Industrial Classification (SIC) codes (used to inform ONS data) does not conform well to marine activities. We have six points a. First, this is a remarkably detailed economic analysis from an organisation that felt constrained not to be able to say that creating jobs in North Wales is a good thing. b. Second, NOMIS is a service provided by the ONS, to give access to the most detailed and up to date UK labour market statistics from official sources. It is government data. "
iv. Given the role of the SUDG in the offshore renewables sector, the RYA would have expected the method of assessment they have developed to have been cascaded to the MDZ project by the Supplementary Tourism and Recreation Assessment, and the previous ES, to ensure like with like comparison that sets the socio-economic impact of the MDZ within a Welsh and UK context. | The SUDG study of socio-economic benefits of marine industries (2019) includes a methodology for estimating the economic contribution of the UK recreation boating sector. This methodology is based information collected by British Marine and on 2015 multipliers calculated in the CEBR Marine Sector Report (2017). This provides an estimate for total employment and GVA contribution of the UK recreation boating sector. Morlais recognises the work done in the SUDG study of socio-economic benefits of marine industries (2019), however, it would be difficult to apply this methodology to Holy Island and the surrounding area. The multipliers utilised in the SUDG study are at a national level and it would not be possible to calculate reliable and efficient multipliers at the local level.
v. The RYA would have expected the assessment to have defined the Gross Value Added, direct employment and trends within the recreational boating sector that uses the coastal and offshore waters of Anglesey. Similarly, we note that the Case Study areas (Chapter 6) are not within moderate inshore recreational boating areas, so are not a good comparison. | Same answer as that for point iv. Also see the note produced by EJ/DB on recreational boating activity and marine energy production comparison.
vi. The assessment should have considered recreational boating as an economic driver to the maritime sector and the implications of the MDZ (both within and outside the Anglesey) to: manufacture, distribution and servicing of recreational craft; suppliers of components, equipment and accessories; together with consumer services (moorings/ storage, boat hire, specialist finance/ insurance, training, brokerage, fuelling, legal services, surveying, etc.). | See p.290 of Morlais closings: "290. Against that background, we turn to the detail. Chapter 25 of the ES addresses the socio-economic impacts of the development. In broad terms, it establishes a baseline, and goes on to assess the socio-economic impacts of the project. The summary is outlined at Table 25-38, and we have just been through many of the benefits. That is the first key document for Welsh Ministers and pausing there we wish to make three points about this: (i) First, the baseline and what was assessed is far broader than recreational water sports. If you look at section 25.4 and in particular para. 62, you will see that this assessment covers Population and Demographics; Employment and GVA; Skills, Training and Education; Housing and Accommodation; Commercial Fisheries; Shipping and Navigation; Tourism; Recreation; and Cultural Heritage. At para. 164 you will see the impacts assessed were in social issues, economic issues, jobs and employment issues, skills and training issues, the effects on tourism, recreation, shipping and fishing and infrastructure issues. The impacts subject to detailed assessment are outlined at para. 171. The key point to highlight is that this is that this is a broad study, look at all sectors of the economy. (ii) A concern has been raised regarding the extent to which water sports recreational amenity users feature in that baseline. We refer you in particular to paras. 25.4.8. That looks at the national, regional and local level. At the regional level, it refers to both kayaking and sailing as a popular regional activities across North Wales (see para. 131). At the local level, sailing is outlined at para. 139, and kayaking at para. 142. The consideration at para. 139 also cross refers to the shipping and navigation chapter of the ES , where you will find a significant amount of detail, both there and in the NRA and NRAA on use by boats. That ES was scoped with PINS, which did ask for more information and tourism and recreation but not boating specifically. (iii) Mr Hill further queried the extent to which long distance cruising from Scotland Northern Ireland, the Isle of Man and the Republic of Ireland featured in the baseline. Again, to the extent these contribute to the local economy through matters such as job creation and visitor spend, that is caught. "
vii. The Key Performance Indicator (Chapter 8) does not include any relevant to the recreational boating sector. | See the commitment to the supplementary kayaking and sailing assessment and monitoring plan (p.295) closings. "our case on socio-economics is this: the mitigations that Menter Môn has put in place. We have gone further than many other developers and agreed to secure by planning condition surveys by which the socioeconomic impacts of the project will be monitored, and mitigated if they are negative. This approach has been agreed with IoACC and as you heard has assuaged their concerns. Both yourself and the Welsh Ministers can take comfort from this – a plan is in place. As Mr Solomon confirmed, the IoACC position is that wherever the baseline is considered to be sitting, mitigation is in place to address any potential negative impact of the scheme. You also have before you a supplementary kayaking and sailing assessment and monitoring plan. We anticipate that specific kayaking and sailing monitoring will form part of the wider plan secured by condition 17 of the deemed planning permission. "
viii. The assessment has not considered the economic benefits and disbenefits with respect to recreational craft repairs, salvage, SAR services, insurance and reputation risk to the Anglesey maritime recreational economy. | See p.288(i) and p.288(iii) of Morlais closings: "(i) Addressing the first point (low carbon energy production), Mr Hill suggested that the RYA also supported action to address climate change, and that this was the only marine renewables project in which the RYA has formally objected. However a. when pressed as to why RYA were objecting to this particular proposal as opposed to other projects (like wind) using a PDE it was because of safety issues (we come back to those) and because this was innovative technology whereas others (such as windfarms) were a known quantity. In our view this suffers from two flaws. First, as we have discussed regarding data gaps in the scientific knowledge (and the opportunity this project provides to remedy that in a highly controlled way) - this project not been done before and there have not been longitudinal studies (a point also made by Ms Wong). This is an opportunity to rectify that. Second, we can see no logical link between the fact that the technology is innovative and whether it will affect the socio-economics of the island. Particularly when matters such as landscape and safety are otherwise assessed and considered acceptable. b. On questioning it became clear from public RYA documents that that the RYA had in fact objected to other tidal projects , and Mr Hill then sought to suggest instead that what he meant was that this is the first time the RYA has gone to a public inquiry level objecting to a TWAO. Given that this is the first TWAO for tidal project that means little. " "(iii) When asked to address the third benefit (job creation), Mr Hill simply said he was not qualified to talk about that and to state that boating had an industry behind it. Again, when pressed, he refused to accept the jobs created were of benefit. We submit that there really is no basis any reasonable party could give for not considering job creation in a deprived area like North Wales is a good thing; Mr Hill’s position and that of the RYA in this regard was risible. It is of course of benefit for all of us for the relevant participants to recognise their limitations and not try to give evidence on matters outside their expertise. However, the fact that RYA feels constrained not to agree with such a basic proposition demonstrates the exceptionally narrow view through which it is approaching this case. "

## FEI_ML012 Trinity Hous
FEI_ML012 ORML1938 – Consultation Response, Trinity House
Feedback | Response
With reference to the above application, I can confirm that Trinity House has no objections, subject to the following conditions being stipulated in any licence issued: | Responses below:
• A separate Navigation Risk Assessment must be produced by the developer of each site/array of devices within the MDZ in accordance with MGN 543 and seek agreement from NRW (in consultation with MCA and Trinity House) that the project risk is deemed to be ALARP. | Noted, the applicant has already committed to an update of the area NRA every 2 years and array specific NRAs prior to device deployment.
• The undertaker must inform NRW in writing at least 5 days prior to the commencement of the authorised project or any part thereof, and within 5 days of completion of the authorised project. | Included in draft ML conditions although the applicant has suggested 7 days in line with historical licence conditions - Condition 11
• The Kingfisher Information Service of Seafish, must be informed of details of the vessel routes, timings and locations relating to the construction of the authorised project or any part thereof by email to kingfisher@seafish.co.uk :- | Included in draft ML conditions - Condition 13
a) at least 14 days prior to the commencement of offshore activities, for inclusion in the Kingfisher Fortnightly Bulletin and offshore hazard awareness data, and;
b) as soon as reasonably practicable and no later than 24 hours of completion of all offshore activities.
Confirmation of notification must be provided to NRW within 5 days.
• The undertaker must ensure that a local notice to mariners is issued at least 14 days prior to the commencement of the authorised project or any part thereof advising of the start date of each and the expected vessel routes from the construction ports to the relevant location. | Included in draft ML conditions - Condition 10
Copies of all notices must be provided to NRW and UKHO within 5 days.
• The undertaker must ensure that local notice to mariners are updated and reissued at weekly intervals during construction activities and at least 5 days before any planned operations (or otherwise agreed) and maintenance works and supplemented with VHF radio broadcasts agreed with the MCA. | Included in draft ML conditions - Condition 10.
Copies of all notices must be provided to NRW and UKHO within 5 days.
• The undertaker must notify the UKHO of the completion (within 14 days) of the authorised project or any part thereof in order that all necessary amendments are made to nautical charts. | Included in draft ML conditions - Condition 11
Copies of all notices must be provided to NRW within 5 days.
• In case of damage to, or destruction or decay of, the authorised project seaward of MHWS or any part thereof, excluding the exposure of cables, the undertaker shall as soon as reasonably practicable and no later than 24 hours following the undertaker becoming aware of any such damage, destruction or decay, notify NRW, MCA, Trinity House, the Kingfisher Information Service of Seafish and the UKHO. | Included in draft ML conditions - Condition 26
• The authorised project shall not commence until the following have been submitted to and approved by NRW. Each programme, statement, plan, protocol, scheme or other detail required to be approved under this condition must be submitted to NRW for approval at least 6 months prior to the commencement of the authorised project except where otherwise stated. | Included in draft ML Conditions but the applicant has proposed 4 months in line with other historical marine licences. This is the Device Deployment Protocol - Condition 1.
1) A plan to be agreed in writing with the NRW following appropriate consultation with Trinity House and the MCA, setting out proposed details of the authorised project, including the:
a) number, dimensions, specification, foundation type(s) and depth for each device,;
b) the grid coordinates of the centre point of the proposed location for each device;
c) proposed layout of all cables; and
d) location and specification of all other aspects of the authorised project.
2) An Aids to Navigation Management Plan to be agreed in writing by NRW following appropriate consultation with Trinity House specifying how the undertaker will ensure compliance with conditions (1) to (4) of ‘Aids to Navigation’ detailed below, from the commencement of construction of the authorised project to the completion of decommissioning. | Included in draft ML Conditions but the applicant has proposed 4 months in line with other historical marine licences. Condition 20
• A construction method statement in accordance with the construction methods assessed in the environmental statement and including details of – | Included in draft ML conditions - Installation Methodology and Cable Management Plan - Condition 21
i) Cable specification, installation and monitoring, to include:
a) technical specification of offshore cables below MHWS;
b) a detailed cable laying plan for the Order limits, incorporating a burial risk assessment encompassing the identification of any cable protection that exceeds 5% of navigable depth referenced to chart datum and, in the event that any area of cable protection exceeding 5% of navigable depth is identified, details of any steps (to be determined following consultation with the MCA and Trinity House) to be taken to ensure existing and future safe navigation is not compromised or such similar assessment to ascertain suitable burial depths and cable laying techniques, including cable protection; and
c) proposals for monitoring offshore cables including cable protection during the operational lifetime of the authorised scheme which includes a risk based approach to the management of unburied or shallow buried cables
• Aids to Navigation:
1) The undertaker shall during the whole period from the commencement of construction of the authorised project to the completion of decommissioning exhibit such lights, marks, sounds, signals and other aids to navigation, and to take such other steps for the prevention of danger to navigation as Trinity House may from time to time direct. | Included in draft ML conditions - Condition 22
2) The undertaker must during the whole period from the commencement of construction of the authorised project to the completion of decommissioning keep Trinity House and NRW informed of progress of the authorised project including; | Secured in various draft ML conditions including but not limited to Conditions 22,23 and 24.
a. notice of commencement of construction of the authorised project within 24 hours of commencement having occurred;
b. notice within 24 hours of any aids to navigation being established by the undertaker; and
c. notice within 5 days of completion of construction of the authorised project.
3) The undertaker must provide reports to Trinity House on the availability of aids to navigation in accordance with the frequencies set out in the aids to navigation management plan, using the reporting system provided by Trinity House. | Included in draft ML conditions - Condition 23
4) The undertaker must during the whole period from the commencement of construction of the authorised project to the completion of decommissioning notify Trinity House and NRW of any failure of the aids to navigation and the timescales and plans for remedying such failures, as soon as possible and no later than 24 hours following the undertaker becoming aware of any such failure.
Included in draft ML conditions - Condition 24
• Colouring of structures:
Must be coloured as directed by Trinity House and detailed in the Aids to Navigation Management Plan. | Noted
• Construction monitoring must include vessel traffic monitoring by automatic identification system for the duration of the construction period. An appropriate report must be submitted to NRW, Trinity House and the MCA at intervals to be agreed by NRW, in consultation with Trinity House and the MCA. | Included in draft ML conditions - Condition 33
• Post construction monitoring must include vessel traffic monitoring by automatic identification system for a duration of three consecutive years following the completion of construction of authorised project, unless otherwise agreed in writing by NRW. An appropriate report must be submitted to NRW, Trinity House and the MCA at the end of each year of the three year period. | Included in draft ML conditions - Condition 34
The above conditions should be applicable to each individual project undertaken within the project envelope. | Noted

## Cadw
Consultation Response, Cadw
Feedback | Response
The additional assessment has confirmed the results of the previous assessment in regard to the impact on Listed Buildings 5713 Ellins Tower, 5284 South Stack Lighthouse and 20081 Tany-y-Cytiau and also scheduled monument AN016 Holyhead Mountain Hut Circles that were included in our previous response: However the new assessment has concluded that there will also be permanent minor adverse impacts on the settings of scheduled monuments AN147 Gogarth Bay round cairn minor and AN019 Caer y Twr and a negligible adverse impact on the setting of Listed Building 20076 Former powder magazine for fog signalling station and enclosure walls. We concur with these conclusions. | Noted

## Cruising Association
Cruising Assocation
Feedback | Response
I am a member of the Regulation and Technical Service Committee of the Cruising Association 9CA) which was founded in 1908, has over 6000 members, mainly active cruising sailors located around the UK, and a clubhouse in London. We are routinely consulted on marine developments in England and Scotland which may impact on Cruising Sailors. In this instance I live on teh Isle of Anglesey and have sailed these waters over 20 years. | Noted
The CA is supportive of developments which increase the supply of energy from renewable sources so long as this does not result in either major long term inconvenience to cruising sailors or significant increased risk. | Noted
In the case of the Morlais Developmetn Zone proposals we share the concerns of the RYA over passage round South Stack. | Noted
Sight lines are poor with a turn of 65 required by vessels from Holyhead bound South around Anglesey or returning. | Noted
The passage around the Stacks is a tidal gate to the east of Holyhead. The Anglesey Pilot (Ralph Morris, Cruising Angelsey and adjoining waters, Imray Laurie Norie and Wilsonn) advises "Once the flood stream has set in its velocity increases until at about 1 hours of flood, it is running at full strength. The strong offset of the stream from the South Stack causes a tide-race, particularly violent over the 20m spur (area of shallower water) extending about 4 cables north west, to run in a wide north westerly arc for the next 3 hours.." | The NRAA looked at the effects of tides, tidal streams and weather on all vessel types, including unpowered recreational craft in accordance with MGN 4543 Annex 2.
The effect of this, taken with the desire to travel with the tide effectively limits the transit time around the Stacks to about 1 hour around slack water. This causes "bunching" of vessels which greatly increaases the chance of collision compares to the situation where vessel transits are unconstrained.
Clearly confining vessels to a narrow corridor as is porposed significantly increases the risk of collision. | The inshore route is not a narrow corridor. Its is 1km wide at its narrowest and over 1.9km wide on average. Two independent NRA's have assessed the risk and considered passage through the inshore route as ALARP or better.
The Navigational Risk Assessment considers the impact of collision but in a way that gives no confidence that it has been given any thought. In particular the list of consequences of collisons in the NRA are exactly the same for all collisions involviing small vessles (fishing vessel or leisue craft). The "worst credible scenario" involves "multiple injuries or a single fatality" which is clearly ill conceived. Small vessels, whether leisure of fishing, sink very rapidly if involved in a collision with a larger or high speed vessel and most will have at least 2 persons on board. There is clearly a significant risk that in such circumstances all person on board will be lost. | Passage through the inshore route has been given considerable consideration throughout the project design as demonstrated by several iterations of the proposed layout to widen the extent of the inshore passage. Since these comments, following design changes and comments from other stakeholders a further NRA, the NRA Addendum (NRAA), has been undertaken. This included separating out powered and unpowered Recreational Vessels for clarity. Unpowered craft included sailing dinghies, kayas, canoes, rowing boats, SUPs etc. In addition, the NRAA further assessed risk to unpowered craft including swamping and capsizing and contact with devices. Finally, the NRAA also looked at the effects of tides, tidal streams and weather on all vessel types, including unpowered recreational craft in accordance with MGN 4543 Annex 2.
With regard to inconvenience, many of our members will be on passage North or south through the Irish Sea and so will dfind the Development Zonr directly on thei path from Bardsey to Holyhead and diverting round the zone would add ~2 miles to the passage (not insignifcant for vessels travelling at 5 or 6 knots). In this respect we ask that, once operational, a vaible direct route is left through the zone on this course, not impeded by exclusion zones. | The displacement of vessels has been considered in the NRAA including vessels that go around the MDZ and this was deemed acceptable by the MCA. However, there will also be gaps between device arrays that will mean that vessels will still be able to transit safely through the MDZ as suggested by the Cruising Association.
In conclusion we support the view of the RYA that the NRW does not assess adequately the risks introduced by the inshore passage restrictions around South Stack and support their objection to the proposal. | Noted although we believe this comment was prior to the CA reviewing the NRAA and is based on the original NRA.