## 2021 Quarterly Report
Biffa Waste Services
Trecatti Landfill Site
Quarterly Report January- March 2021
Introduction
The Trecatti landfill site is located in a disused opencast coal workings close to Merthyr Tydfil and a very short distance from the town of Dowlais. The site contains 8 leachate wells (LW), 13 groundwater (GW) boreholes and a further 26 gas boreholes (BH) around the perimeter. The landfill also has an on-site Leachate Treatment Plant (LTP) which was built in 1996 to treat leachate extracted from the landfill site.
Under permit RP3733PC Version 11, Biffa Waste Services are required to submit a Quarterly Report for the site for each three month period rolling January-March 2021
The report has been split into 9 chapters of which follows:
1. Waste Characterization
2. Leachate
3. Surface Water
4. Ground Water
5. Gas Borehole Monitoring
6. FID
7. Engine Emissions
8. Biogenie
9. Asbestos and Dust Monitoring
10. Inclinometer
1. Waste Characterization
Waste characterisation is the process in which the different components of waste is analysed, all waste streams on site are visually inspected at either the weighbridge or upon disposal at the working face. At the site all waste enquiries have been assessed in line with regulations to meet the Waste Acceptance Criteria as required by section 2.3.3 of the permit.
2. Leachate
A) Leachate Wells
Under the permit, leachate is monitored at the discharge effluent from the leachate treatment plant as well as monitored from all 8 wells. There are no permit limits for the Wells to comply with in regards to quality, however they are continually reviewed and are as expected. Please see ‘Leachate Data’ for quarterly quality results. Leachate levels are monitored on a monthly basis, the period for January-March 2021 is shown in the table below.
Month | Well | Sample | Base | Level
January | 1 | 81703010 | 328.44 | 349.02
| 2 | 81703020 | 330.34 | 352.7
| 3 | 81703030 | 330.34 | 358.81
| 4 | 81703040 | 333.19 | 358.69
| 5 | 81703050 | 369.65 | 372.55
| 6 | 81703060 | 372.16 | 376.6
| 7 | 81703070 | 341 | 358.92
| 8 | 81703080 | 331 | 361.26
February | 1 | 81703010 | 328.44 | 346.01
| 2 | 81703020 | 330.34 | 346.92
| 3 | 81703030 | 330.34 | 358.03
| 4 | 81703040 | 333.19 | 361.9
| 5 | 81703050 | 369.65 | 373.21
| 6 | 81703060 | 372.16 | 377.06
| 7 | 81703070 | 341 | 357.23
| 8 | 81703080 | 331 | 360.58
March | 1 | 81703010 | 328.44 | 349.44
| 2 | 81703020 | 330.34 | 349.48
| 3 | 81703030 | 330.34 | 358.65
| 4 | 81703040 | 333.19 | 362.12
| 5 | 81703050 | 369.65 | 373.28
| 6 | 81703060 | 372.16 | 376.75
| 7 | 81703070 | 341 | 358.46
| 8 | 81703080 | 331 | 362.48
All wells were compliant during the quarter. Leachate samples for wells 7 and 8 were unable to be obtained in March due to pump maintenance repairs.
B) Treated leachate/Effluent
The permit requires treated leachate/effluent to be sampled and recorded on a monthly basis. The effluent is sampled for the following contaminants:
pH
Suspended Solids
Ammoniacal Nitrogen
Temperature
Total Metals
Cyanide
Sulphide
Sulphate
The table below are the results for this quarterly period
| pH | Suspended Solids | Ammoniacal Nitrogen | Temperature | Total Metals | Cyanide | Sulphide | Sulphate
| 6 to 11 | 400mg/l | 40mg/l | 43˚C | 2mg/l | 1mg/l | 2mg/l | 1000mg/l
January | 7.4 | - | 0.44 | 21.4 | 0.53 | 0.043 | <0.020 | 83.4
February | 7 | 93 | <0.41 | 21.7 | 0.465 | 0.034 | 0.025 | 157
March | 6.9 | 21 | 1.16 | 24.8 | 0.53 | 0.029 | <0.020 | 101
Results show that there were no breaches for this quarterly period, all parameters are within the discharge consent limits.
The result for suspended solids in January was repeated by the laboratory due a specific limit breach and they were unable to validate original result therefore the labs
could not report the result. Following the repeated test there was insufficient sample remaining for further analysis.
3. Surface Water
The permit requires surface water discharge to be sampled and recorded on a monthly basis and testing for the following contaminants:
pH
Suspended Solids
Ammonia Nitrogen
Chemical Oxygen Demand (COD)
Following an audit conducted by the formally known Environment Agency (now Natural Resource Wales) in 2008 the following monitoring reports were amended and as follows:
· SWA (81702001) North Western boundary downstream discharge point
· SWB (81702002) Eastern boundary downstream discharge point
· SWC (81702003) Northern boundary upstream monitoring point
· SW Monocell (81702014) side-riser and sump -operational areas of monocell
During the audit it was agreed that as the operator is unable to control the external influences from these four monitoring points, it was decided that the rate of flow and volume limit requirements would be removed. However volume of surface water pumped off site to the discharge point SWA would be recorded and if applicable reported
The results for the discharge points are shown in the table below.
There were no results for Sample points A, B, C and D in February and March due to insufficient flow.
SWA | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
January | 7.1 | 9 | <0.41 | <11.0
February | Insufficient
March | Insufficient
SWB | pH | Suspended Solids | Ammoniacal Nitrogen | COD
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l
January | 7.1 | 10 | <0.41 | 19
February | Insufficient
March | Insufficient
SWC | pH | Suspended Solids | Ammoniacal Nitrogen | COD | SWC is not a discharge point - so does not have limits and is run off from the common land area.
January | 7 | 2 | <0.41 | 18
February | Insufficient
March | Insufficient
SWD | pH | Suspended Solids | Ammoniacal Nitrogen | COD | SWD is not a discharge point - so does not have limits and is run off from the common land area.
January | 7.1 | 7 | <0.41 | 12
February | Insufficient
March | Insufficient
Monocell | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Asbestos Fibres
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l | none detectable
January | Sample point removed
February | Sample point removed
March | Sample point removed
No samples were obtained from the monocell lagoon during the quarter. Filling operations have commenced into this area so the sample point has had to be removed.
All surface water was compliant in January.
4. Groundwater
Groundwater levels are monitored on a monthly basis and quality is monitored on a quarterly basis at boreholes GW 1 – 13. The results for the groundwater levels from January -March 2020 are shown below.
No groundwater dip has been carried out on groundwater well 3 during January, February and March.
The pump was removed for electrical testing in March, the well has slightly collapsed making level monitoring difficult and the pump can not currently be re installed.
|  | Sample | Top of borehole (mAOD) | Dip from top (m) | Top of GW (mAOD)
January | 1 | 81701110 | 433.14 | 148.17 | 284.97
| 2 | 81701120 | 417.04 | 143.44 | 273.6
| 3 | 81701130 | 409.95
| 4 | 81701140 | 424.74 | 139.45 | 285.29
| 5 | 81701150 | 437.4 | 175.25 | 262.15
| 6 | 81701160 | 399.88 | 127.62 | 272.26
| 7 | 81701170 | 445.83 | 153.66 | 292.17
| 8 | 81701180 | 384.07 | 196.13 | 187.94
| 9 | 81701209 | 413.97 | 118.82 | 295.15
| 10 | 81701210 | 426.57 | 152.81 | 273.76
| 11 | 81701211 | 443.44 | 133.55 | 309.89
| 12 | 81701212 | 444.4 | 168.74 | 275.66
| 13 | 81701213 | 385.81 | 107.82 | 277.99
February | 1 | 81701110 | 433.14 | 148.2 | 284.94
| 2 | 81701120 | 417.04 | 143.87 | 273.17
| 3 | 81701130 | 409.95
| 4 | 81701140 | 424.74 | 139.45 | 285.29
| 5 | 81701150 | 437.4 | 177.22 | 260.18
| 6 | 81701160 | 399.88 | 128.62 | 271.26
| 7 | 81701170 | 445.83 | 153.7 | 292.13
| 8 | 81701180 | 384.07 | 96.88 | 287.19
| 9 | 81701209 | 413.97 | 144.2 | 269.77
| 10 | 81701210 | 426.57 | 154.73 | 271.84
| 11 | 81701211 | 443.44 | 128.79 | 314.65
| 12 | 81701212 | 444.4 | 168.99 | 275.41
| 13 | 81701213 | 385.81 | 107.93 | 277.88
March | 1 | 81701110 | 433.14 | 148.2 | 284.94
| 2 | 81701120 | 417.04 | 143.41 | 273.63
| 3 | 81701130 | 409.95
| 4 | 81701140 | 424.74 | 140.49 | 284.25
| 5 | 81701150 | 437.4 | 177.58 | 259.82
| 6 | 81701160 | 399.88 | 139.27 | 260.61
| 7 | 81701170 | 445.83 | 157.36 | 288.47
| 8 | 81701180 | 384.07 | 97.07 | 287
| 9 | 81701209 | 413.97 | 118.97 | 295
| 10 | 81701210 | 426.57 | 153.95 | 272.62
| 11 | 81701211 | 443.44 | 171.61 | 271.83
| 12 | 81701212 | 444.4 | 168.69 | 275.71
| 13 | 81701213 | 385.81 | 107.8 | 278.01
The groundwater samples were analysed by ALS Environmental, the results are available on the tab labelled ‘Groundwater Quality’. Due to slow re-charge rates, and reduced water levels, samples could not be taken from 81701130, 81701150, 81701170, 81701209, 81701210 & 81701211. Groundwater 2 breached Ammoniacal Nitrogen as highlighted in red. A schedule 5 has been attached for this non-compliance.
| NH4 | Chloride | Cadmium | Mecoprop | Toluene | Naphthalene | Xylene
Permit Limit | 17mg/l | 650 mg/l | 0.16 µg/l | 1 µg/l | 65 µg/l | 1 µg/l | 15µg/l
81701120 | 17.7 | 247 | <0.07 | 0.33 | <1.00 | <1.00 | <1.00
5. Gas Borehole Monitoring
There are 26 gas boreholes which are located around the perimeter of the landfill site of which are monitored on a monthly basis using a fully calibrated Gas Analyser (GA5000) as required by the permit. The atmospheric pressure, concentration of gases including: Methane (CH4) Carbon Dioxide (CO2) and Oxygen (O2) are parameters which were all recorded for each of the 26 gas boreholes. The findings are found in the table below. Meteorological data and ground conditions are also recorded.
81701001 | CH4 | CO2 | 81701002 | CH4 | CO2 | 81701003 | CH4 | CO2 | 81701004 | CH4 | CO2
Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 3% V.V | 10% V.V
January | 0.1 | 1.7 | January | 0.1 | 6.3 | January | 0.1 | 0.1 | January | 7.1 | 8.1
February | 0.1 | 0.7 | February | 0.1 | 5.3 | February | 0.1 | 1.8 | February | 12 | 10.5
March | 0.1 | 1.2 | March | 0.1 | 3.2 | March | 0.1 | 1.7 | March | 11.7 | 9.2
81701005 | CH4 | CO2 | 81701006 | CH4 | CO2 | 81701007 | CH4 | CO2 | 81701008 | CH4 | CO2
Permit Limit | 13% V.V | 17% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% | 12%
January | 0.1 | 5 | January | 0.1 | 6.9 | January | 0.1 | 5.4 | January | 0.1 | 5.6
February | 0.1 | 4.1 | February | 0.1 | 6.9 | February | 0.1 | 4.4 | February | 0.1 | 7.3
March | 3.2 | 4.6 | March | 0.1 | 7.1 | March | 0.1 | 5.8 | March | 0.1 | 4
81701009 | CH4 | CO2 | 81701010 | CH4 | CO2 | 81701011 | CH4 | CO2 | 81701012 | CH4 | CO2
Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V
January | 0.1 | 1.8 | January | 0.1 | 2.2 | January | 0.1 | 1.8 | January | 0.1 | 0.5
February | 0.1 | 2.7 | February | 0.1 | 2.9 | February | 0.1 | 0.3 | February | 0.1 | 0.5
March | 0.1 | 1.6 | March | 0.1 | 2 | March | 0.1 | 1.2 | March | 0.1 | 0.5
81701013 | CH4 | CO2 | 81701014 | CH4 | CO2 | 81701015 | CH4 | CO2 | 81701016 | CH4 | CO2
Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Action Limit | 1% V.V | 16.7% V.V | Action Limit | 10.2 | 11.2
January | 0.1 | 0.1 | January | 0.1 | 1.9 | January | 0.1 | 7.1 | January | 1.3 | 6.6
February | 0.1 | 2.2 | February | 0 | 0.9 | February | 0 | 6.6 | February | 1.3 | 3.7
March | 0.1 | 1.2 | March | 0.1 | 5.6 | March | 0.1 | 6.5 | March | 1 | 5.1
81701017 | CH4 | CO2 | 81701018 | CH4 | CO2 | 81701019 | CH4 | CO2 | 81701020 | CH4 | CO2
Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V
January | 0.1 | 3.4 | January | 0.1 | 5.4 | January | 0.1 | 7.6 | January | 0.4 | 2.2
February | 0 | 2.1 | February | 0 | 6 | February | 0.1 | 7.4 | February | 0.3 | 1.6
March | 0.1 | 3.1 | March | 0.1 | 5.8 | March | 0.1 | 7.4 | March | 0.1 | 0.4
81701021 | CH4 | CO2 | 81701022 | CH4 | CO2 | 81701023 | CH4 | CO2 | 81701024 | CH4 | CO2
Action Limit | 24.6 | 19.2 | Permit Limit | 1% V.V | 10% V.V | Permit Limit | 1% V.V | 10% V.V | Action Limit | 29.7 | 9.7
January | 23.8 | 20.2 | January | 1.5 | 1.3 | January | 0.1 | 2.5 | January | 8.5 | 9.1
February | 21.8 | 18.5 | February | 14.2 | 14.9 | February | 0.1 | 2.1 | February | 8.6 | 8.2
March | 23.4 | 20 | March | 10 | 10.1 | March | 0.1 | 2.4 | March | 7.4 | 8.1
81701025 | CH4 | CO2 | 81701026 | CH4 | CO2
Action Limit | 57.5 | 12.7 | Action Limit | 37.9 | 15.9
January | 37.7 | 9.1 | January | 6.2 | 14.9
February | 34 | 10.1 | February | 1 | 5.3
March | 34 | 12.4 | March | 4.4 | 14.4
All the above boreholes were compliant this quarter.
6. FID Monitoring
A FID (Flame Ionisation Detector) is used to sample at 27 locations around the landfill site and the following results were recorded for this quarter,
where the maximum reading has been shown in the table below, the full data set is found in the ‘Ambient Air Monitoring’ tab
| Month | FID
max reading
| January | 35
| February | 20
| March | 30
The highest max recording was 35ppm during January
7. Engine Emissions
Date of Monitoring: 05/02/2021
| Sampling time | Carbon Monoxide (mg(N)m-3) | Oxides of Nitrogen (mg(N)m-3) | Oxygen (%)
Emission limit |  | 1500 | 650 | -
Engine 1 | Not Tested
Engine3 | Not Tested
| Sampling time | Carbon Monoxide (mg(N)m-3) | Oxides of Nitrogen (mg(N)m-3) | Oxygen (%)
Emission limit |  | 1400 | 500
Engine 4 | 09:54-10:01 | 1045 | 355 | 6.97
Engine 5 | 10:08-10:15 | 928 | 494 | 7.18
Engine 6 | 10:18-10:25 | 1098 | 442 | 7.28
Engine 7 | Not Tested
Taking into account the overall uncertainties from LFTGNO8v2, all emissions results are compliant.
Where appropriate, an assessment of air ingress into the system has been undertaken
8. Biogenie
Samples are required for surface water collected from the contaminated soils pad.
Chemtest Ltd carry out Monthly Analysis on behalf of Biogenie.
There are two sample points on the site permit
1. Process Water from Biopiles
2. Surface Water Lagoon
SW Point 1 Biopiles | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Oil/Grease
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l | Non Visible
January | 8.2 | 40 | 45 | 30 | Non Visible
February | 7.8 | 56 | 2.8 | 53 | Non Visible
March | 7.9 | 35 | 2.6 | 49 | Non Visible
SW Point 2, Lagoon | pH | Suspended Solids | Ammoniacal Nitrogen | COD | Oil/Grease
Permit limit | 6 to 8 | 100 mg/l | 5mg/l | 120 mg/l | Non Visible
January | 8.3 | 71 | 45 | 26 | Non Visible
February | 7.9 | 52 | 2.9 | 35 | Non Visible
March | 7.9 | 42 | 2.7 | 49 | Non Visible
As the above results show, the pH level and Ammoniacal Nitrogen were above the compliance limits in January, no discharge to the site surface waters was made.
Pumping Permits are raised by Biogenie and authorised by Biffa Personnel when they want to pump from SW 2 Lagoon into the 385 Lagoon and is signed off
by Biffa only when the process water is compliant. Any non compliant water is sent to sewer.
The 385 Lagoon is currently being engineered so the void can be used for landfill operations.
9. Asbestos and Dust Monitoring
Asbestos monitoring is required 6 monthly and was submitted in the Q4 2020 report.
Dust Monitoring Results
Dust monitoring is required 6 monthly and was submitted in the Q4 2020 report.
10. Inclinometer
SLR carried out inclinometer monitoring during March 2021.
As stated in previous reports it is not possible to advance the inclinometer probe further than 6.5m depth in Inclinometer 2, due to a blockage, a decision was made to use the January 2020 data as the new “base set” data for this instrument, resulting in a shallower data set.
Please see below the results of displacement over time at each location as displayed in graphical form.

## Surface Water Quality
Sample | Sample_Description | Description | 2021-01-28 | Unit
81702001 | SW POINT A WEST | OIL AND GREASE (VISUAL) | no
81702001 | SW POINT A WEST | pH | 7.1
81702001 | SW POINT A WEST | Suspended Solids | 9 | mg/l
81702001 | SW POINT A WEST | BOD + ATU (5 DAY) | <1 | mg/l
81702001 | SW POINT A WEST | CHLORIDE AS Cl | <3.7 | mg/l
81702001 | SW POINT A WEST | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81702001 | SW POINT A WEST | ELECTRICAL CONDUCTIVITY | <30.0 | uS/cm
81702001 | SW POINT A WEST | CHEMICAL OXYGEN DEMAND | <11.0 | mg/l
81702001 | SW POINT A WEST | TEMPERATURE | 8 | DegC
81702002 | SW POINT B EAST | OIL AND GREASE (VISUAL) | no
81702002 | SW POINT B EAST | pH | 7.1
81702002 | SW POINT B EAST | Suspended Solids | 10 | mg/l
81702002 | SW POINT B EAST | BOD + ATU (5 DAY) | <1 | mg/l
81702002 | SW POINT B EAST | CHLORIDE AS Cl | <3.7 | mg/l
81702002 | SW POINT B EAST | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81702002 | SW POINT B EAST | ELECTRICAL CONDUCTIVITY | <30.0 | uS/cm
81702002 | SW POINT B EAST | CHEMICAL OXYGEN DEMAND | 19 | mg/l
81702002 | SW POINT B EAST | TEMPERATURE | 8.2 | DegC
81702003 | SW POINT C UPSTREAM | OIL AND GREASE (VISUAL) | no
81702003 | SW POINT C UPSTREAM | pH | 7
81702003 | SW POINT C UPSTREAM | Suspended Solids | 2 | mg/l
81702003 | SW POINT C UPSTREAM | BOD + ATU (5 DAY) | 1 | mg/l
81702003 | SW POINT C UPSTREAM | CHLORIDE AS Cl | <3.7 | mg/l
81702003 | SW POINT C UPSTREAM | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81702003 | SW POINT C UPSTREAM | ELECTRICAL CONDUCTIVITY | <30.0 | uS/cm
81702003 | SW POINT C UPSTREAM | CHEMICAL OXYGEN DEMAND | 18 | mg/l
81702003 | SW POINT C UPSTREAM | TEMPERATURE | 7.9 | DegC
81702009 | SW POINT D | OIL AND GREASE (VISUAL) | no
81702009 | SW POINT D | pH | 7.1
81702009 | SW POINT D | Suspended Solids | 7 | mg/l
81702009 | SW POINT D | BOD + ATU (5 DAY) | <1 | mg/l
81702009 | SW POINT D | CHLORIDE AS Cl | <3.7 | mg/l
81702009 | SW POINT D | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81702009 | SW POINT D | ELECTRICAL CONDUCTIVITY | <30.0 | uS/cm
81702009 | SW POINT D | CHEMICAL OXYGEN DEMAND | 12 | mg/l
81702009 | SW POINT D | TEMPERATURE | 8.1 | DegC

## Groundwater Quality
Sample | Sample_Description | Code | Description | 2021-02-25 | Unit
81701110 | GW1 | 2 | pH | 7.8
81701110 | GW1 | 15 | CHLORIDE AS Cl | 10.7 | mg/l
81701110 | GW1 | 16 | ALKALINITY AS CaCO3 | 369 | mg/l
81701110 | GW1 | 17 | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81701110 | GW1 | 19 | NITRITE AS N | <0.08 | mg/l
81701110 | GW1 | 20 | NITRATE AS N | <0.7 | mg/l
81701110 | GW1 | 29 | CHROMIUM, TOTAL AS CR | <0.002 | mg/l
81701110 | GW1 | 39 | CALCIUM TOTAL AS CA | 48.5 | mg/l
81701110 | GW1 | 40 | MAGNESIUM AS MG | 45.6 | mg/l
81701110 | GW1 | 41 | SODIUM AS NA | 5.46 | mg/l
81701110 | GW1 | 42 | POTASSIUM AS K | 22.6 | mg/l
81701110 | GW1 | 50 | SULPHATE AS SO4 | <4.4 | mg/l
81701110 | GW1 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701110 | GW1 | 54 | ELECTRICAL CONDUCTIVITY | 607 | uS/cm
81701110 | GW1 | 70T | IRON, TOTAL AS FE | <0.025 | mg/l
81701110 | GW1 | 70V | MANGANESE AS MN | 0.12 | mg/l
81701110 | GW1 | 70Z | NICKEL TOTAL AS NI | <0.0010 | mg/l
81701110 | GW1 | 101 | TEMPERATURE | 7.4 | DegC
81701110 | GW1 | 716 | COPPER TOAL AS CU | <0.0018 | mg/l
81701110 | GW1 | 719 | ZINC | 0.052 | mg/l
81701110 | GW1 | 725 | CADMIUM, TOTAL AS CD | <0.00007 | mg/l
81701110 | GW1 | 731 | LEAD TOTAL AS PB | <0.0003 | mg/l
81701110 | GW1 | GG8 | MECOPROP | <0.04 | ug/l
81701110 | GW1 | GTP | Toluene | <1.00 | ug/l
81701110 | GW1 | GUP | Naphthalene | <1.00 | ug/l
81701110 | GW1 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701110 | GW1 | KKH | Tritium | <5.0 | Bq/l
81701120 | GW2 | 2 | pH | 7.3
81701120 | GW2 | 15 | CHLORIDE AS Cl | 247 | mg/l
81701120 | GW2 | 16 | ALKALINITY AS CaCO3 | 833 | mg/l
81701120 | GW2 | 17 | AMMONIACAL NITROGEN AS N | 17.7 | mg/l
81701120 | GW2 | 19 | NITRITE AS N | <0.08 | mg/l
81701120 | GW2 | 20 | NITRATE AS N | <0.7 | mg/l
81701120 | GW2 | 29 | CHROMIUM, TOTAL AS CR | 0.004 | mg/l
81701120 | GW2 | 39 | CALCIUM TOTAL AS CA | 100 | mg/l
81701120 | GW2 | 40 | MAGNESIUM AS MG | 96.3 | mg/l
81701120 | GW2 | 41 | SODIUM AS NA | 115 | mg/l
81701120 | GW2 | 42 | POTASSIUM AS K | 108 | mg/l
81701120 | GW2 | 50 | SULPHATE AS SO4 | 13.1 | mg/l
81701120 | GW2 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701120 | GW2 | 54 | ELECTRICAL CONDUCTIVITY | 1970 | uS/cm
81701120 | GW2 | 70T | IRON, TOTAL AS FE | 0.337 | mg/l
81701120 | GW2 | 70V | MANGANESE AS MN | 0.16 | mg/l
81701120 | GW2 | 70Z | NICKEL TOTAL AS NI | 0.025 | mg/l
81701120 | GW2 | 716 | COPPER TOAL AS CU | 0.0084 | mg/l
81701120 | GW2 | 719 | ZINC | 3 | mg/l
81701120 | GW2 | 725 | CADMIUM, TOTAL AS CD | <0.00007 | mg/l
81701120 | GW2 | 731 | LEAD TOTAL AS PB | <0.0003 | mg/l
81701120 | GW2 | GG8 | MECOPROP | 0.33 | ug/l
81701120 | GW2 | GTP | Toluene | <1.00 | ug/l
81701120 | GW2 | GUP | Naphthalene | <1.00 | ug/l
81701120 | GW2 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701120 | GW2 | KKH | Tritium | 79.3 | Bq/l
81701140 | GW4 | 2 | pH | 7
81701140 | GW4 | 15 | CHLORIDE AS Cl | 24.3 | mg/l
81701140 | GW4 | 16 | ALKALINITY AS CaCO3 | 677 | mg/l
81701140 | GW4 | 17 | AMMONIACAL NITROGEN AS N | 1.22 | mg/l
81701140 | GW4 | 19 | NITRITE AS N | <0.08 | mg/l
81701140 | GW4 | 20 | NITRATE AS N | <0.7 | mg/l
81701140 | GW4 | 29 | CHROMIUM, TOTAL AS CR | <0.002 | mg/l
81701140 | GW4 | 39 | CALCIUM TOTAL AS CA | 194 | mg/l
81701140 | GW4 | 40 | MAGNESIUM AS MG | 159 | mg/l
81701140 | GW4 | 41 | SODIUM AS NA | 17.1 | mg/l
81701140 | GW4 | 42 | POTASSIUM AS K | 73.1 | mg/l
81701140 | GW4 | 50 | SULPHATE AS SO4 | 604 | mg/l
81701140 | GW4 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701140 | GW4 | 54 | ELECTRICAL CONDUCTIVITY | 1870 | uS/cm
81701140 | GW4 | 70T | IRON, TOTAL AS FE | 0.082 | mg/l
81701140 | GW4 | 70V | MANGANESE AS MN | 1.6 | mg/l
81701140 | GW4 | 70Z | NICKEL TOTAL AS NI | 0.0099 | mg/l
81701140 | GW4 | 716 | COPPER TOAL AS CU | 0.0025 | mg/l
81701140 | GW4 | 719 | ZINC | 0.14 | mg/l
81701140 | GW4 | 725 | CADMIUM, TOTAL AS CD | <0.00007 | mg/l
81701140 | GW4 | 731 | LEAD TOTAL AS PB | <0.0003 | mg/l
81701140 | GW4 | GG8 | MECOPROP | <0.04 | ug/l
81701140 | GW4 | GTP | Toluene | <1.00 | ug/l
81701140 | GW4 | GUP | Naphthalene | <1.00 | ug/l
81701140 | GW4 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701140 | GW4 | KKH | Tritium | 7.1 | Bq/l
81701160 | GW6 | 2 | pH | 6.8
81701160 | GW6 | 15 | CHLORIDE AS Cl | 160 | mg/l
81701160 | GW6 | 16 | ALKALINITY AS CaCO3 | 489 | mg/l
81701160 | GW6 | 17 | AMMONIACAL NITROGEN AS N | 2.91 | mg/l
81701160 | GW6 | 19 | NITRITE AS N | <0.08 | mg/l
81701160 | GW6 | 20 | NITRATE AS N | <0.7 | mg/l
81701160 | GW6 | 29 | CHROMIUM, TOTAL AS CR | <0.002 | mg/l
81701160 | GW6 | 39 | CALCIUM TOTAL AS CA | 143 | mg/l
81701160 | GW6 | 40 | MAGNESIUM AS MG | 96.8 | mg/l
81701160 | GW6 | 41 | SODIUM AS NA | 64.7 | mg/l
81701160 | GW6 | 42 | POTASSIUM AS K | 55.1 | mg/l
81701160 | GW6 | 50 | SULPHATE AS SO4 | 308 | mg/l
81701160 | GW6 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701160 | GW6 | 54 | ELECTRICAL CONDUCTIVITY | 1630 | uS/cm
81701160 | GW6 | 70T | IRON, TOTAL AS FE | 0.028 | mg/l
81701160 | GW6 | 70V | MANGANESE AS MN | 1.5 | mg/l
81701160 | GW6 | 70Z | NICKEL TOTAL AS NI | 0.016 | mg/l
81701160 | GW6 | 716 | COPPER TOAL AS CU | 0.003 | mg/l
81701160 | GW6 | 719 | ZINC | 0.67 | mg/l
81701160 | GW6 | 725 | CADMIUM, TOTAL AS CD | 0.00019 | mg/l
81701160 | GW6 | 731 | LEAD TOTAL AS PB | 0.0005 | mg/l
81701160 | GW6 | GG8 | MECOPROP | 0.05 | ug/l
81701160 | GW6 | GTP | Toluene | 1.09 | ug/l
81701160 | GW6 | GUP | Naphthalene | <1.00 | ug/l
81701160 | GW6 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701160 | GW6 | KKH | Tritium | 14.6 | Bq/l
81701180 | GW8 | 2 | pH | 7
81701180 | GW8 | 15 | CHLORIDE AS Cl | 678 | mg/l
81701180 | GW8 | 16 | ALKALINITY AS CaCO3 | 547 | mg/l
81701180 | GW8 | 17 | AMMONIACAL NITROGEN AS N | <0.41 | mg/l
81701180 | GW8 | 19 | NITRITE AS N | <0.08 | mg/l
81701180 | GW8 | 20 | NITRATE AS N | <0.7 | mg/l
81701180 | GW8 | 29 | CHROMIUM, TOTAL AS CR | <0.002 | mg/l
81701180 | GW8 | 39 | CALCIUM TOTAL AS CA | 209 | mg/l
81701180 | GW8 | 40 | MAGNESIUM AS MG | 138 | mg/l
81701180 | GW8 | 41 | SODIUM AS NA | 232 | mg/l
81701180 | GW8 | 42 | POTASSIUM AS K | 69.3 | mg/l
81701180 | GW8 | 50 | SULPHATE AS SO4 | 200 | mg/l
81701180 | GW8 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701180 | GW8 | 54 | ELECTRICAL CONDUCTIVITY | 2990 | uS/cm
81701180 | GW8 | 70T | IRON, TOTAL AS FE | <0.025 | mg/l
81701180 | GW8 | 70V | MANGANESE AS MN | 0.032 | mg/l
81701180 | GW8 | 70Z | NICKEL TOTAL AS NI | 0.0067 | mg/l
81701180 | GW8 | 716 | COPPER TOAL AS CU | 0.0023 | mg/l
81701180 | GW8 | 719 | ZINC | 0.39 | mg/l
81701180 | GW8 | 725 | CADMIUM, TOTAL AS CD | 0.00019 | mg/l
81701180 | GW8 | 731 | LEAD TOTAL AS PB | 0.0005 | mg/l
81701180 | GW8 | GG8 | MECOPROP | <0.04 | ug/l
81701180 | GW8 | GTP | Toluene | <1.00 | ug/l
81701180 | GW8 | GUP | Naphthalene | <1.00 | ug/l
81701180 | GW8 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701180 | GW8 | KKH | Tritium | <5.0 | Bq/l
81701212 | GW12 | 2 | pH | 7.1
81701212 | GW12 | 15 | CHLORIDE AS Cl | 40.4 | mg/l
81701212 | GW12 | 16 | ALKALINITY AS CaCO3 | 681 | mg/l
81701212 | GW12 | 17 | AMMONIACAL NITROGEN AS N | 0.73 | mg/l
81701212 | GW12 | 19 | NITRITE AS N | <0.08 | mg/l
81701212 | GW12 | 20 | NITRATE AS N | <0.7 | mg/l
81701212 | GW12 | 29 | CHROMIUM, TOTAL AS CR | <0.002 | mg/l
81701212 | GW12 | 39 | CALCIUM TOTAL AS CA | 162 | mg/l
81701212 | GW12 | 40 | MAGNESIUM AS MG | 137 | mg/l
81701212 | GW12 | 41 | SODIUM AS NA | 27.4 | mg/l
81701212 | GW12 | 42 | POTASSIUM AS K | 73.2 | mg/l
81701212 | GW12 | 50 | SULPHATE AS SO4 | 448 | mg/l
81701212 | GW12 | 51 | ORTHOPHOSPHATE AS P | <0.6 | mg/l
81701212 | GW12 | 54 | ELECTRICAL CONDUCTIVITY | 1770 | uS/cm
81701212 | GW12 | 70T | IRON, TOTAL AS FE | <0.025 | mg/l
81701212 | GW12 | 70V | MANGANESE AS MN | 0.81 | mg/l
81701212 | GW12 | 70Z | NICKEL TOTAL AS NI | 0.0044 | mg/l
81701212 | GW12 | 716 | COPPER TOAL AS CU | <0.0018 | mg/l
81701212 | GW12 | 719 | ZINC | 0.23 | mg/l
81701212 | GW12 | 725 | CADMIUM, TOTAL AS CD | <0.00007 | mg/l
81701212 | GW12 | 731 | LEAD TOTAL AS PB | <0.0003 | mg/l
81701212 | GW12 | GG8 | MECOPROP | <0.04 | ug/l
81701212 | GW12 | GTP | Toluene | <1.00 | ug/l
81701212 | GW12 | GUP | Naphthalene | <1.00 | ug/l
81701212 | GW12 | GUR | Xylene (o+p+m) | <1.00 | ug/l
81701212 | GW12 | KKH | Tritium | <5.0 | Bq/l

## Leachate Level
Sample | Description | Date | Top_of_Well | Dip_from_top | Base_of_Well | Depth_fm_base | Leachate_Level
81703010 | leachate well 1 | 2021-01-20 | 397.68 | 48.66 | 328.44 | 20.58 | 349.02
81703020 | leachate well 2 | 2021-01-14 | 400.26 | 47.56 | 330.34 | 22.36 | 352.7
81703030 | leachate well 3 | 2021-01-14 | 398.92 | 40.11 | 330.34 | 28.47 | 358.81
81703040 | leachate well 4 | 2021-01-14 | 400.57 | 41.88 | 333.19 | 25.5 | 358.69
81703050 | leachate well 5 | 2021-01-14 | 398.54 | 25.99 | 369.65 | 2.9 | 372.55
81703060 | leachate well 6 | 2021-01-14 | 404.48 | 27.88 | 372.16 | 4.44 | 376.6
81703070 | leachate well 7 | 2021-01-14 | 396.13 | 37.21 | 341 | 17.92 | 358.92
81703080 | leachate well 8 | 2021-01-14 | 400.7 | 39.44 | 331 | 30.26 | 361.26
81703010 | leachate well 1 | 2021-02-08 | 397.68 | 51.67 | 328.44 | 17.57 | 346.01
81703020 | leachate well 2 | 2021-02-08 | 400.26 | 53.34 | 330.34 | 16.58 | 346.92
81703030 | leachate well 3 | 2021-02-08 | 398.92 | 40.89 | 330.34 | 27.69 | 358.03
81703040 | leachate well 4 | 2021-02-08 | 400.57 | 38.67 | 333.19 | 28.71 | 361.9
81703050 | leachate well 5 | 2021-02-08 | 398.54 | 25.33 | 369.65 | 3.56 | 373.21
81703060 | leachate well 6 | 2021-02-08 | 404.48 | 27.42 | 372.16 | 4.9 | 377.06
81703070 | leachate well 7 | 2021-02-08 | 396.13 | 38.9 | 341 | 16.23 | 357.23
81703080 | leachate well 8 | 2021-02-08 | 400.7 | 40.12 | 331 | 29.58 | 360.58
81703010 | leachate well 1 | 2021-03-19 | 397.68 | 48.24 | 328.44 | 21 | 349.44
81703020 | leachate well 2 | 2021-03-19 | 400.26 | 50.78 | 330.34 | 19.14 | 349.48
81703030 | leachate well 3 | 2021-03-19 | 398.92 | 40.27 | 330.34 | 28.31 | 358.65
81703040 | leachate well 4 | 2021-03-19 | 400.57 | 38.45 | 333.19 | 28.93 | 362.12
81703050 | leachate well 5 | 2021-03-19 | 398.54 | 25.26 | 369.65 | 3.63 | 373.28
81703060 | leachate well 6 | 2021-03-19 | 404.48 | 27.73 | 372.16 | 4.59 | 376.75
81703070 | leachate well 7 | 2021-03-19 | 396.13 | 37.67 | 341 | 17.46 | 358.46
81703080 | leachate well 8 | 2021-03-19 | 400.7 | 38.22 | 331 | 31.48 | 362.48

## Gas Borehole
Borehole | Description | Date | Time | CH4 | CO2 | O2 | Bal | Atmos | Relative | Precipitation
81701001 | GAS BOREHOLE 1 | 2021-01-28 | 11:50 | 0.1 | 1.7 | 17.5 | 80.7 | 963 | -0.05 | RAIN
81701001 | GAS BOREHOLE 1 | 2021-02-22 | 13:58 | 0.1 | 0.7 | 16.3 | 82.9 | 975 | 0.29 | NONE
81701001 | GAS BOREHOLE 1 | 2021-03-29 | 14:15 | 0.1 | 1.2 | 21.1 | 77.6 | 986 | -0.05 | DRIZZLE
81701002 | GAS BOREHOLE 2 | 2021-01-28 | 11:44 | 0.1 | 6.3 | 1.1 | 92.5 | 963 | 0.26 | RAIN
81701002 | GAS BOREHOLE 2 | 2021-02-22 | 14:09 | 0.1 | 5.3 | 0.5 | 94.1 | 976 | 1.15 | NONE
81701002 | GAS BOREHOLE 2 | 2021-03-29 | 14:09 | 0.1 | 3.2 | 12.7 | 84 | 985 | 0.09 | DRIZZLE
81701003 | GAS BOREHOLE 3 | 2021-01-28 | 11:55 | 0.1 | 0.1 | 22.4 | 77.4 | 961 | 0.09 | RAIN
81701003 | GAS BOREHOLE 3 | 2021-02-22 | 13:45 | 0.1 | 1.8 | 18 | 80.1 | 974 | 0.32 | NONE
81701003 | GAS BOREHOLE 3 | 2021-03-29 | 14:20 | 0.1 | 1.7 | 14.7 | 83.5 | 984 | 0.14 | DRIZZLE
81701004 | GAS BOREHOLE 4 | 2021-01-28 | 12:06 | 7.1 | 8.1 | 11.5 | 73.3 | 957 | 0 | RAIN
81701004 | GAS BOREHOLE 4 | 2021-02-22 | 13:23 | 12 | 10.5 | 2.2 | 75.3 | 969 | 0.5 | NONE
81701004 | GAS BOREHOLE 4 | 2021-03-29 | 14:34 | 11.7 | 9.2 | 3.7 | 75.4 | 980 | -0.41 | DRIZZLE
81701005 | GAS BOREHOLE 5 | 2021-01-28 | 11:15 | 0.1 | 5 | 4.5 | 90.4 | 957 | 0.05 | RAIN
81701005 | GAS BOREHOLE 5 | 2021-02-22 | 15:33 | 0.1 | 4.1 | 1 | 94.8 | 969 | -0.77 | NONE
81701005 | GAS BOREHOLE 5 | 2021-03-29 | 13:36 | 3.2 | 4.6 | 0.6 | 91.6 | 980 | -0.62 | DRIZZLE
81701006 | GAS BOREHOLE 6 | 2021-01-28 | 11:16 | 0.1 | 6.9 | 15.3 | 77.7 | 957 | 0.56 | RAIN
81701006 | GAS BOREHOLE 6 | 2021-02-22 | 15:30 | 0.1 | 6.9 | 15.7 | 77.3 | 969 | -0.02 | NONE
81701006 | GAS BOREHOLE 6 | 2021-03-29 | 13:39 | 0.1 | 7.1 | 14.9 | 77.9 | 979 | 0.14 | DRIZZLE
81701007 | GAS BOREHOLE 7 | 2021-01-28 | 11:19 | 0.1 | 5.4 | 12 | 82.5 | 956 | 0.07 | RAIN
81701007 | GAS BOREHOLE 7 | 2021-02-22 | 15:26 | 0.1 | 4.4 | 14.7 | 80.8 | 969 | 0.03 | NONE
81701007 | GAS BOREHOLE 7 | 2021-03-29 | 13:43 | 0.1 | 5.8 | 16.8 | 77.3 | 979 | -0.03 | DRIZZLE
81701008 | GAS BOREHOLE 8 | 2021-01-28 | 12:20 | 0.1 | 5.6 | 14.5 | 79.8 | 956 | -0.05 | RAIN
81701008 | GAS BOREHOLE 8 | 2021-02-22 | 15:21 | 0.1 | 7.3 | 16.3 | 76.3 | 968 | -0.03 | NONE
81701008 | GAS BOREHOLE 8 | 2021-03-29 | 13:45 | 0.1 | 4 | 19.8 | 76.1 | 978 | -0.03 | DRIZZLE
81701009 | GAS BOREHOLE 9 | 2021-01-28 | 11:22 | 0.1 | 1.8 | 20.2 | 77.9 | 955 | 0.22 | RAIN
81701009 | GAS BOREHOLE 9 | 2021-02-22 | 15:17 | 0.1 | 2.7 | 17.5 | 79.7 | 967 | 0.6 | NONE
81701009 | GAS BOREHOLE 9 | 2021-03-29 | 13:48 | 0.1 | 1.6 | 21.1 | 77.2 | 978 | 0.05 | DRIZZLE
81701010 | GAS BOREHOLE 10 | 2021-01-28 | 11:24 | 0.1 | 2.2 | 20.7 | 77 | 955 | 0.36 | RAIN
81701010 | GAS BOREHOLE 10 | 2021-02-22 | 15:12 | 0.1 | 2.9 | 18.2 | 78.8 | 967 | 0.09 | NONE
81701010 | GAS BOREHOLE 10 | 2021-03-29 | 13:50 | 0.1 | 2 | 20.3 | 77.6 | 977 | -0.07 | DRIZZLE
81701011 | GAS BOREHOLE 11 | 2021-01-28 | 11:27 | 0.1 | 1.8 | 20.5 | 77.6 | 955 | 0.12 | RAIN
81701011 | GAS BOREHOLE 11 | 2021-02-22 | 15:08 | 0.1 | 0.3 | 22 | 77.6 | 967 | 0.29 | NONE
81701011 | GAS BOREHOLE 11 | 2021-03-29 | 13:52 | 0.1 | 1.2 | 21 | 77.7 | 977 | 0.07 | DRIZZLE
81701012 | GAS BOREHOLE 12 | 2021-01-28 | 11:29 | 0.1 | 0.5 | 21.8 | 77.6 | 956 | 1.09 | RAIN
81701012 | GAS BOREHOLE 12 | 2021-02-22 | 15:04 | 0.1 | 0.5 | 20.7 | 78.7 | 968 | 0.14 | NONE
81701012 | GAS BOREHOLE 12 | 2021-03-29 | 13:54 | 0.1 | 0.5 | 21.7 | 77.7 | 978 | 0.17 | DRIZZLE
81701013 | GAS BOREHOLE 13 | 2021-01-28 | 11:31 | 0.1 | 0.1 | 22.6 | 77.2 | 956 | -0.12 | RAIN
81701013 | GAS BOREHOLE 13 | 2021-02-22 | 14:59 | 0.1 | 2.2 | 17.5 | 80.2 | 968 | -1.66 | NONE
81701013 | GAS BOREHOLE 13 | 2021-03-29 | 13:56 | 0.1 | 1.2 | 19.8 | 78.9 | 978 | -0.12 | DRIZZLE
81701014 | GAS BOREHOLE 14 | 2021-01-28 | 11:33 | 0.1 | 1.9 | 7.5 | 90.5 | 957 | 0.63 | RAIN
81701014 | GAS BOREHOLE 14 | 2021-02-22 | 14:41 | 0 | 0.9 | 18.4 | 80.7 | 970 | 0.48 | NONE
81701014 | GAS BOREHOLE 14 | 2021-03-29 | 13:59 | 0.1 | 5.6 | 15.7 | 78.6 | 980 | 0.02 | DRIZZLE
81701015 | GAS BOREHOLE 15 | 2021-01-28 | 11:36 | 0.1 | 7.1 | 16.2 | 76.6 | 958 | 0.19 | RAIN
81701015 | GAS BOREHOLE 15 | 2021-02-22 | 14:36 | 0 | 6.6 | 15.4 | 78 | 971 | 0.44 | NONE
81701015 | GAS BOREHOLE 15 | 2021-03-29 | 14:01 | 0.1 | 6.5 | 17.6 | 75.8 | 980 | 0.14 | DRIZZLE
81701016 | GAS BOREHOLE 16 | 2021-01-28 | 11:38 | 1.3 | 6.6 | 0.5 | 91.6 | 958 | -0.05 | RAIN
81701016 | GAS BOREHOLE 16 | 2021-02-22 | 14:30 | 1.3 | 3.7 | 0.3 | 94.7 | 971 | -0.02 | NONE
81701016 | GAS BOREHOLE 16 | 2021-03-29 | 14:03 | 1 | 5.1 | 0.5 | 93.4 | 981 | -0.44 | DRIZZLE
81701017 | GAS BOREHOLE 17 | 2021-01-28 | 11:40 | 0.1 | 3.4 | 19.1 | 77.4 | 959 | 0.12 | RAIN
81701017 | GAS BOREHOLE 17 | 2021-02-22 | 14:24 | 0 | 2.1 | 19.9 | 78 | 972 | 0.24 | NONE
81701017 | GAS BOREHOLE 17 | 2021-03-29 | 14:05 | 0.1 | 3.1 | 19.1 | 77.7 | 982 | 0.03 | DRIZZLE
81701018 | GAS BOREHOLE 18 | 2021-01-28 | 11:41 | 0.1 | 5.4 | 16.6 | 77.9 | 961 | 0.02 | RAIN
81701018 | GAS BOREHOLE 18 | 2021-02-22 | 14:19 | 0 | 6 | 14.8 | 79.2 | 973 | 0.44 | NONE
81701018 | GAS BOREHOLE 18 | 2021-03-29 | 14:07 | 0.1 | 5.8 | 17.3 | 76.8 | 983 | 0.02 | DRIZZLE
81701019 | GAS BOREHOLE 19 | 2021-01-28 | 11:47 | 0.1 | 7.6 | 12.7 | 79.6 | 962 | 0.02 | RAIN
81701019 | GAS BOREHOLE 19 | 2021-02-22 | 14:05 | 0.1 | 7.4 | 11.1 | 81.4 | 974 | 0.22 | NONE
81701019 | GAS BOREHOLE 19 | 2021-03-29 | 14:12 | 0.1 | 7.4 | 10 | 82.5 | 985 | 0.02 | DRIZZLE
81701020 | GAS BOREHOLE 20 | 2021-01-28 | 11:53 | 0.4 | 2.2 | 17.7 | 79.7 | 963 | 0.07 | RAIN
81701020 | GAS BOREHOLE 20 | 2021-02-22 | 13:51 | 0.3 | 1.6 | 17.9 | 80.2 | 974 | 1.45 | NONE
81701020 | GAS BOREHOLE 20 | 2021-03-29 | 14:18 | 0.1 | 0.4 | 21.2 | 78.3 | 985 | 5.2 | DRIZZLE
81701021 | GAS BOREHOLE 21 | 2021-01-28 | 11:57 | 23.8 | 20.2 | 2.4 | 53.6 | 961 | 0.31 | RAIN
81701021 | GAS BOREHOLE 21 | 2021-02-22 | 13:41 | 21.8 | 18.5 | 2.3 | 57.4 | 973 | 0.48 | NONE
81701021 | GAS BOREHOLE 21 | 2021-03-29 | 14:22 | 23.4 | 20 | 1.5 | 55.1 | 983 | 0.02 | DRIZZLE
81701022 | GAS BOREHOLE 22 | 2021-01-28 | 11:59 | 1.5 | 1.3 | 20.9 | 76.3 | 960 | 0.14 | RAIN
81701022 | GAS BOREHOLE 22 | 2021-02-22 | 13:37 | 14.2 | 14.9 | 5 | 65.9 | 972 | 0.32 | NONE
81701022 | GAS BOREHOLE 22 | 2021-03-29 | 14:28 | 10 | 10.1 | 10.3 | 69.6 | 983 | -0.05 | DRIZZLE
81701023 | GAS BOREHOLE 23 | 2021-01-28 | 12:01 | 0.1 | 2.5 | 5.1 | 92.3 | 953 | 0.15 | RAIN
81701023 | GAS BOREHOLE 23 | 2021-02-22 | 13:33 | 0.1 | 2.1 | 4.2 | 93.6 | 971 | 0.44 | NONE
81701023 | GAS BOREHOLE 23 | 2021-03-29 | 14:30 | 0.1 | 2.4 | 7.3 | 90.2 | 982 | -0.02 | DRIZZLE
81701024 | GAS BOREHOLE 24 | 2021-01-28 | 12:04 | 8.5 | 9.1 | 0.8 | 81.6 | 958 | 0.19 | RAIN
81701024 | GAS BOREHOLE 24 | 2021-02-22 | 13:29 | 8.6 | 8.2 | 0.2 | 83 | 970 | -2.67 | NONE
81701024 | GAS BOREHOLE 24 | 2021-03-29 | 14:32 | 7.4 | 8.1 | 0.5 | 84 | 981 | -0.14 | DRIZZLE
81701025 | GAS BOREHOLE 25 | 2021-01-28 | 12:08 | 37.7 | 9.1 | 0.4 | 52.8 | 956 | 0.1 | RAIN
81701025 | GAS BOREHOLE 25 | 2021-02-22 | 13:20 | 34 | 10.1 | 0.3 | 55.6 | 969 | 0.26 | NONE
81701025 | GAS BOREHOLE 25 | 2021-03-29 | 14:36 | 34 | 12.4 | 0.4 | 53.2 | 980 | -0.09 | DRIZZLE
81701026 | GAS BOREHOLE 26 | 2021-01-28 | 12:10 | 6.2 | 14.9 | 1.1 | 77.8 | 956 | 0.14 | RAIN
81701026 | GAS BOREHOLE 26 | 2021-02-22 | 13:16 | 1 | 5.3 | 3.3 | 90.4 | 969 | 1.42 | NONE
81701026 | GAS BOREHOLE 26 | 2021-03-29 | 14:39 | 4.4 | 14.4 | 1.3 | 79.9 | 979 | 1.49 | DRIZZLE

## Leachate Quality
Sample | Sample_Description | Code | Description | 2021-02-25 | Unit
81703010 | Leachate well 1 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703010 | Leachate well 1 | 0F4 | TOTAL ORGANIC CARBON | 625 | mg/l
81703010 | Leachate well 1 | 2 | pH | 7.8
81703010 | Leachate well 1 | 04Q | AMMONIACAL NITROGEN | 1540 | mg/l
81703010 | Leachate well 1 | 10 | BOD + ATU (5 DAY) | 243 | mg/l
81703010 | Leachate well 1 | 16 | ALKALINITY AS CaCO3 | 4540 | mg/l
81703010 | Leachate well 1 | 29 | CHROMIUM, TOTAL AS CR | 0.198 | mg/l
81703010 | Leachate well 1 | 39 | CALCIUM TOTAL AS CA | 80.7 | mg/l
81703010 | Leachate well 1 | 40 | MAGNESIUM AS MG | 109 | mg/l
81703010 | Leachate well 1 | 41 | SODIUM AS NA | 2180 | mg/l
81703010 | Leachate well 1 | 42 | POTASSIUM AS K | 756 | mg/l
81703010 | Leachate well 1 | 54 | ELECTRICAL CONDUCTIVITY | 20900 | uS/cm
81703010 | Leachate well 1 | 70 | CHEMICAL OXYGEN DEMAND | 2610 | mg/l
81703010 | Leachate well 1 | 70T | IRON, TOTAL AS FE | 2.6 | mg/l
81703010 | Leachate well 1 | 70V | MANGANESE AS MN | 0.15 | mg/l
81703010 | Leachate well 1 | 70Z | NICKEL TOTAL AS NI | 0.33 | mg/l
81703010 | Leachate well 1 | 716 | COPPER TOAL AS CU | <0.018 | mg/l
81703010 | Leachate well 1 | 719 | ZINC | <0.060 | mg/l
81703010 | Leachate well 1 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703010 | Leachate well 1 | 731 | LEAD TOTAL AS PB | <0.0030 | mg/l
81703010 | Leachate well 1 | CAA | SULPHATE AS SO4 | 18.6 | mg/l
81703010 | Leachate well 1 | GED | BENTAZONE | <20.0 | ug/l
81703010 | Leachate well 1 | GFA | BROMOXYNIL | <20.0 | ug/l
81703010 | Leachate well 1 | GFW | 2,3,6-TBA | <20.0 | ug/l
81703010 | Leachate well 1 | GFY | 2,4-D | <20.0 | ug/l
81703010 | Leachate well 1 | GFZ | 2,4-DB | <20.0 | ug/l
81703010 | Leachate well 1 | GG3 | 2,4,5-T | <20.0 | ug/l
81703010 | Leachate well 1 | GG8 | MECOPROP | 35.5 | ug/l
81703010 | Leachate well 1 | GG9 | DICAMBA | <20.0 | ug/l
81703010 | Leachate well 1 | GGA | MCPA | <20.0 | ug/l
81703010 | Leachate well 1 | GGB | DICHLORPROP | <20.0 | ug/l
81703010 | Leachate well 1 | GGC | MCPB | <20.0 | ug/l
81703010 | Leachate well 1 | GGD | IOXYNIL | <20.0 | ug/l
81703010 | Leachate well 1 | GGE | CLOPYRALID | <20.0 | ug/l
81703010 | Leachate well 1 | GKW | BENAZOLIN | <20.0 | ug/l
81703010 | Leachate well 1 | GKX | FENOPROP | <20.0 | ug/l
81703010 | Leachate well 1 | GKY | TRICLOPYR | <20.0 | ug/l
81703010 | Leachate well 1 | GKZ | FLUROXYPYR | <20.0 | ug/l
81703010 | Leachate well 1 | GS3 | Dichlorodifluoromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GS4 | Chloromethane | <10.0 | ug/l
81703010 | Leachate well 1 | GS5 | Vinyl Chloride | <2.50 | ug/l
81703010 | Leachate well 1 | GS6 | Bromomethane | <5.00 | ug/l
81703010 | Leachate well 1 | GS7 | Chloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GS8 | Trichlorofluoromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GS9 | 1,1-Dichloroethene | <5.00 | ug/l
81703010 | Leachate well 1 | GSS | Dichloromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GSU | MTBE | <5.00 | ug/l
81703010 | Leachate well 1 | GSV | trans-1,2-Dichloroethene | <5.00 | ug/l
81703010 | Leachate well 1 | GSW | 1,1-Dichloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GSX | 1,2-Dichloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GSY | 2,2-Dichloropropane | <5.00 | ug/l
81703010 | Leachate well 1 | GSZ | Bromochloromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GT1 | Chloroform | <5.00 | ug/l
81703010 | Leachate well 1 | GT2 | 1,1,1-Trichloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GT6 | 1,1-Dichloropropene | <5.00 | ug/l
81703010 | Leachate well 1 | GT7 | Carbon Tetrachloride | <5.00 | ug/l
81703010 | Leachate well 1 | GT8 | 1,2-Dichloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GT9 | Benzene | 36.3 | ug/l
81703010 | Leachate well 1 | GTJ | Trichloroethene | <5.00 | ug/l
81703010 | Leachate well 1 | GTK | 1,2-Dichloropropane | <5.00 | ug/l
81703010 | Leachate well 1 | GTL | Dibromomethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTM | Bromodichloromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTN | cis-1,3-Dichloropropene | <5.00 | ug/l
81703010 | Leachate well 1 | GTP | Toluene | 14.9 | ug/l
81703010 | Leachate well 1 | GTQ | trans-1,3-Dichloropropene | <5.00 | ug/l
81703010 | Leachate well 1 | GTR | 1,1,2-Trichloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTT | Tetrachloroethene | <5.00 | ug/l
81703010 | Leachate well 1 | GTU | 1,3-Dichloropropane | <5.00 | ug/l
81703010 | Leachate well 1 | GTV | Dibromochloromethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTW | 1,2-Dibromoethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTX | Chlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GTY | 1,1,1,2-Tetrachloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GTZ | Ethyl Benzene | 19.4 | ug/l
81703010 | Leachate well 1 | GU0 | m and p-xylene | 32.2 | ug/l
81703010 | Leachate well 1 | GU1 | O-Xylene | 13.8 | ug/l
81703010 | Leachate well 1 | GU2 | Styrene | <5.00 | ug/l
81703010 | Leachate well 1 | GU3 | Bromoform | <5.00 | ug/l
81703010 | Leachate well 1 | GU4 | iso-Propylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GU5 | 1,1,2,2-Tetrachloroethane | <5.00 | ug/l
81703010 | Leachate well 1 | GU6 | 1,2,3-Trichloropropane | <5.00 | ug/l
81703010 | Leachate well 1 | GU7 | Bromobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GU8 | n-propylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GU9 | 2-Chlorotoluene | <5.00 | ug/l
81703010 | Leachate well 1 | GUA | 1,3,5-Trimethylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUB | 4-Chlorotoluene | <5.00 | ug/l
81703010 | Leachate well 1 | GUC | tert-Butylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUD | 1,2,4-Trimethylbenzene | 15.8 | ug/l
81703010 | Leachate well 1 | GUE | sec-butylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUF | p-isopropyltoluene | 7.4 | ug/l
81703010 | Leachate well 1 | GUG | 1,3-Dichlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUH | 1,4-Dichlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUJ | n-butylbenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUK | 1,2-Dichlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUL | 1,2-Dibromo-3-chloropropane | <10.0 | ug/l
81703010 | Leachate well 1 | GUM | 1,2,4-Trichlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUN | Hexachlorobutadiene | <5.00 | ug/l
81703010 | Leachate well 1 | GUP | Naphthalene | 242 | ug/l
81703010 | Leachate well 1 | GUQ | 1,2,3-Trichlorobenzene | <5.00 | ug/l
81703010 | Leachate well 1 | GUR | Xylene (o+p+m) | 46 | ug/l
81703010 | Leachate well 1 | KKH | Tritium | 552 | Bq/l
81703010 | Leachate well 1 | V11 | CHLORIDE AS CL | 3590 | mg/l
81703020 | Leachate well 2 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703020 | Leachate well 2 | 0F4 | TOTAL ORGANIC CARBON | 576 | mg/l
81703020 | Leachate well 2 | 2 | pH | 6.9
81703020 | Leachate well 2 | 04Q | AMMONIACAL NITROGEN | 297 | mg/l
81703020 | Leachate well 2 | 10 | BOD + ATU (5 DAY) | 603 | mg/l
81703020 | Leachate well 2 | 16 | ALKALINITY AS CaCO3 | 1400 | mg/l
81703020 | Leachate well 2 | 29 | CHROMIUM, TOTAL AS CR | 0.037 | mg/l
81703020 | Leachate well 2 | 39 | CALCIUM TOTAL AS CA | 482 | mg/l
81703020 | Leachate well 2 | 40 | MAGNESIUM AS MG | 62.8 | mg/l
81703020 | Leachate well 2 | 41 | SODIUM AS NA | 723 | mg/l
81703020 | Leachate well 2 | 42 | POTASSIUM AS K | 315 | mg/l
81703020 | Leachate well 2 | 54 | ELECTRICAL CONDUCTIVITY | 7820 | uS/cm
81703020 | Leachate well 2 | 70 | CHEMICAL OXYGEN DEMAND | 1540 | mg/l
81703020 | Leachate well 2 | 70T | IRON, TOTAL AS FE | 5.4 | mg/l
81703020 | Leachate well 2 | 70V | MANGANESE AS MN | 1.3 | mg/l
81703020 | Leachate well 2 | 70Z | NICKEL TOTAL AS NI | 0.13 | mg/l
81703020 | Leachate well 2 | 716 | COPPER TOAL AS CU | <0.018 | mg/l
81703020 | Leachate well 2 | 719 | ZINC | <0.060 | mg/l
81703020 | Leachate well 2 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703020 | Leachate well 2 | 731 | LEAD TOTAL AS PB | 0.006 | mg/l
81703020 | Leachate well 2 | GED | BENTAZONE | <20.0 | ug/l
81703020 | Leachate well 2 | GFA | BROMOXYNIL | <20.0 | ug/l
81703020 | Leachate well 2 | GFW | 2,3,6-TBA | <20.0 | ug/l
81703020 | Leachate well 2 | GFY | 2,4-D | <20.0 | ug/l
81703020 | Leachate well 2 | GFZ | 2,4-DB | <20.0 | ug/l
81703020 | Leachate well 2 | GG3 | 2,4,5-T | <20.0 | ug/l
81703020 | Leachate well 2 | GG8 | MECOPROP | <16.0 | ug/l
81703020 | Leachate well 2 | GG9 | DICAMBA | <20.0 | ug/l
81703020 | Leachate well 2 | GGA | MCPA | <20.0 | ug/l
81703020 | Leachate well 2 | GGB | DICHLORPROP | <20.0 | ug/l
81703020 | Leachate well 2 | GGC | MCPB | <20.0 | ug/l
81703020 | Leachate well 2 | GGD | IOXYNIL | <20.0 | ug/l
81703020 | Leachate well 2 | GGE | CLOPYRALID | <20.0 | ug/l
81703020 | Leachate well 2 | GKW | BENAZOLIN | <20.0 | ug/l
81703020 | Leachate well 2 | GKX | FENOPROP | <20.0 | ug/l
81703020 | Leachate well 2 | GKY | TRICLOPYR | <20.0 | ug/l
81703020 | Leachate well 2 | GKZ | FLUROXYPYR | <20.0 | ug/l
81703020 | Leachate well 2 | GS3 | Dichlorodifluoromethane | <1.00 | ug/l
81703020 | Leachate well 2 | GS4 | Chloromethane | <2.00 | ug/l
81703020 | Leachate well 2 | GS5 | Vinyl Chloride | <0.500 | ug/l
81703020 | Leachate well 2 | GS6 | Bromomethane | <1.00 | ug/l
81703020 | Leachate well 2 | GS7 | Chloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GS8 | Trichlorofluoromethane | <1.00 | ug/l
81703020 | Leachate well 2 | GS9 | 1,1-Dichloroethene | <1.00 | ug/l
81703020 | Leachate well 2 | GSS | Dichloromethane | 32.1 | ug/l
81703020 | Leachate well 2 | GSU | MTBE | <1.00 | ug/l
81703020 | Leachate well 2 | GSV | trans-1,2-Dichloroethene | <1.00 | ug/l
81703020 | Leachate well 2 | GSW | 1,1-Dichloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GSX | 1,2-Dichloroethane | 3.11 | ug/l
81703020 | Leachate well 2 | GSY | 2,2-Dichloropropane | <1.00 | ug/l
81703020 | Leachate well 2 | GSZ | Bromochloromethane | <1.00 | ug/l
81703020 | Leachate well 2 | GT1 | Chloroform | <1.00 | ug/l
81703020 | Leachate well 2 | GT2 | 1,1,1-Trichloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GT6 | 1,1-Dichloropropene | <1.00 | ug/l
81703020 | Leachate well 2 | GT7 | Carbon Tetrachloride | <1.00 | ug/l
81703020 | Leachate well 2 | GT8 | 1,2-Dichloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GT9 | Benzene | 61.5 | ug/l
81703020 | Leachate well 2 | GTJ | Trichloroethene | <1.00 | ug/l
81703020 | Leachate well 2 | GTK | 1,2-Dichloropropane | <1.00 | ug/l
81703020 | Leachate well 2 | GTL | Dibromomethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTM | Bromodichloromethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTN | cis-1,3-Dichloropropene | <1.00 | ug/l
81703020 | Leachate well 2 | GTP | Toluene | 117 | ug/l
81703020 | Leachate well 2 | GTQ | trans-1,3-Dichloropropene | <1.00 | ug/l
81703020 | Leachate well 2 | GTR | 1,1,2-Trichloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTT | Tetrachloroethene | <1.00 | ug/l
81703020 | Leachate well 2 | GTU | 1,3-Dichloropropane | <1.00 | ug/l
81703020 | Leachate well 2 | GTV | Dibromochloromethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTW | 1,2-Dibromoethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTX | Chlorobenzene | 4.04 | ug/l
81703020 | Leachate well 2 | GTY | 1,1,1,2-Tetrachloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GTZ | Ethyl Benzene | 81.8 | ug/l
81703020 | Leachate well 2 | GU0 | m and p-xylene | 150 | ug/l
81703020 | Leachate well 2 | GU1 | O-Xylene | 52.7 | ug/l
81703020 | Leachate well 2 | GU2 | Styrene | 9.53 | ug/l
81703020 | Leachate well 2 | GU3 | Bromoform | <1.00 | ug/l
81703020 | Leachate well 2 | GU4 | iso-Propylbenzene | 5.51 | ug/l
81703020 | Leachate well 2 | GU5 | 1,1,2,2-Tetrachloroethane | <1.00 | ug/l
81703020 | Leachate well 2 | GU6 | 1,2,3-Trichloropropane | <1.00 | ug/l
81703020 | Leachate well 2 | GU7 | Bromobenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GU8 | n-propylbenzene | 5.21 | ug/l
81703020 | Leachate well 2 | GU9 | 2-Chlorotoluene | <1.00 | ug/l
81703020 | Leachate well 2 | GUA | 1,3,5-Trimethylbenzene | 17.3 | ug/l
81703020 | Leachate well 2 | GUB | 4-Chlorotoluene | <1.00 | ug/l
81703020 | Leachate well 2 | GUC | tert-Butylbenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GUD | 1,2,4-Trimethylbenzene | 59.4 | ug/l
81703020 | Leachate well 2 | GUE | sec-butylbenzene | 1.25 | ug/l
81703020 | Leachate well 2 | GUF | p-isopropyltoluene | 45.9 | ug/l
81703020 | Leachate well 2 | GUG | 1,3-Dichlorobenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GUH | 1,4-Dichlorobenzene | 4.89 | ug/l
81703020 | Leachate well 2 | GUJ | n-butylbenzene | 1.26 | ug/l
81703020 | Leachate well 2 | GUK | 1,2-Dichlorobenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GUL | 1,2-Dibromo-3-chloropropane | <2.00 | ug/l
81703020 | Leachate well 2 | GUM | 1,2,4-Trichlorobenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GUN | Hexachlorobutadiene | <1.00 | ug/l
81703020 | Leachate well 2 | GUP | Naphthalene | 26.9 | ug/l
81703020 | Leachate well 2 | GUQ | 1,2,3-Trichlorobenzene | <1.00 | ug/l
81703020 | Leachate well 2 | GUR | Xylene (o+p+m) | 203 | ug/l
81703020 | Leachate well 2 | KKH | Tritium | 58.7 | Bq/l
81703020 | Leachate well 2 | V10 | SULPHATE AS SO4 | 535 | mg/l
81703020 | Leachate well 2 | V11 | CHLORIDE AS CL | 1560 | mg/l
81703030 | Leachate well 3 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703030 | Leachate well 3 | 0F4 | TOTAL ORGANIC CARBON | 411 | mg/l
81703030 | Leachate well 3 | 2 | pH | 7.6
81703030 | Leachate well 3 | 04Q | AMMONIACAL NITROGEN | 624 | mg/l
81703030 | Leachate well 3 | 10 | BOD + ATU (5 DAY) | 410 | mg/l
81703030 | Leachate well 3 | 16 | ALKALINITY AS CaCO3 | 1830 | mg/l
81703030 | Leachate well 3 | 29 | CHROMIUM, TOTAL AS CR | 0.077 | mg/l
81703030 | Leachate well 3 | 39 | CALCIUM TOTAL AS CA | 236 | mg/l
81703030 | Leachate well 3 | 40 | MAGNESIUM AS MG | 63.6 | mg/l
81703030 | Leachate well 3 | 41 | SODIUM AS NA | 1000 | mg/l
81703030 | Leachate well 3 | 42 | POTASSIUM AS K | 377 | mg/l
81703030 | Leachate well 3 | 54 | ELECTRICAL CONDUCTIVITY | 10400 | uS/cm
81703030 | Leachate well 3 | 70 | CHEMICAL OXYGEN DEMAND | 1480 | mg/l
81703030 | Leachate well 3 | 70T | IRON, TOTAL AS FE | 1.9 | mg/l
81703030 | Leachate well 3 | 70V | MANGANESE AS MN | 0.69 | mg/l
81703030 | Leachate well 3 | 70Z | NICKEL TOTAL AS NI | 0.12 | mg/l
81703030 | Leachate well 3 | 716 | COPPER TOAL AS CU | 0.023 | mg/l
81703030 | Leachate well 3 | 719 | ZINC | 0.077 | mg/l
81703030 | Leachate well 3 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703030 | Leachate well 3 | 731 | LEAD TOTAL AS PB | 0.0045 | mg/l
81703030 | Leachate well 3 | GED | BENTAZONE | <1.00 | ug/l
81703030 | Leachate well 3 | GFA | BROMOXYNIL | <1.00 | ug/l
81703030 | Leachate well 3 | GFW | 2,3,6-TBA | <1.00 | ug/l
81703030 | Leachate well 3 | GFY | 2,4-D | <1.00 | ug/l
81703030 | Leachate well 3 | GFZ | 2,4-DB | <1.00 | ug/l
81703030 | Leachate well 3 | GG3 | 2,4,5-T | <1.00 | ug/l
81703030 | Leachate well 3 | GG8 | MECOPROP | 11.6 | ug/l
81703030 | Leachate well 3 | GG9 | DICAMBA | <1.00 | ug/l
81703030 | Leachate well 3 | GGA | MCPA | <1.00 | ug/l
81703030 | Leachate well 3 | GGB | DICHLORPROP | 1.72 | ug/l
81703030 | Leachate well 3 | GGC | MCPB | <1.00 | ug/l
81703030 | Leachate well 3 | GGD | IOXYNIL | <1.00 | ug/l
81703030 | Leachate well 3 | GGE | CLOPYRALID | <1.00 | ug/l
81703030 | Leachate well 3 | GKW | BENAZOLIN | <1.00 | ug/l
81703030 | Leachate well 3 | GKX | FENOPROP | <1.00 | ug/l
81703030 | Leachate well 3 | GKY | TRICLOPYR | <1.00 | ug/l
81703030 | Leachate well 3 | GKZ | FLUROXYPYR | <1.00 | ug/l
81703030 | Leachate well 3 | GS3 | Dichlorodifluoromethane | <5.00 | ug/l
81703030 | Leachate well 3 | GS4 | Chloromethane | <10.0 | ug/l
81703030 | Leachate well 3 | GS5 | Vinyl Chloride | <2.50 | ug/l
81703030 | Leachate well 3 | GS6 | Bromomethane | <5.00 | ug/l
81703030 | Leachate well 3 | GS7 | Chloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GS8 | Trichlorofluoromethane | <5.00 | ug/l
81703030 | Leachate well 3 | GS9 | 1,1-Dichloroethene | <5.00 | ug/l
81703030 | Leachate well 3 | GSS | Dichloromethane | 7.55 | ug/l
81703030 | Leachate well 3 | GSU | MTBE | <5.00 | ug/l
81703030 | Leachate well 3 | GSV | trans-1,2-Dichloroethene | <5.00 | ug/l
81703030 | Leachate well 3 | GSW | 1,1-Dichloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GSX | 1,2-Dichloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GSY | 2,2-Dichloropropane | <5.00 | ug/l
81703030 | Leachate well 3 | GSZ | Bromochloromethane | <5.00 | ug/l
81703030 | Leachate well 3 | GT1 | Chloroform | <5.00 | ug/l
81703030 | Leachate well 3 | GT2 | 1,1,1-Trichloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GT6 | 1,1-Dichloropropene | <5.00 | ug/l
81703030 | Leachate well 3 | GT7 | Carbon Tetrachloride | <5.00 | ug/l
81703030 | Leachate well 3 | GT8 | 1,2-Dichloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GT9 | Benzene | 30.6 | ug/l
81703030 | Leachate well 3 | GTJ | Trichloroethene | <5.00 | ug/l
81703030 | Leachate well 3 | GTK | 1,2-Dichloropropane | <5.00 | ug/l
81703030 | Leachate well 3 | GTL | Dibromomethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTM | Bromodichloromethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTN | cis-1,3-Dichloropropene | <5.00 | ug/l
81703030 | Leachate well 3 | GTP | Toluene | 39.3 | ug/l
81703030 | Leachate well 3 | GTQ | trans-1,3-Dichloropropene | <5.00 | ug/l
81703030 | Leachate well 3 | GTR | 1,1,2-Trichloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTT | Tetrachloroethene | <5.00 | ug/l
81703030 | Leachate well 3 | GTU | 1,3-Dichloropropane | <5.00 | ug/l
81703030 | Leachate well 3 | GTV | Dibromochloromethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTW | 1,2-Dibromoethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTX | Chlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GTY | 1,1,1,2-Tetrachloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GTZ | Ethyl Benzene | 22.7 | ug/l
81703030 | Leachate well 3 | GU0 | m and p-xylene | 41 | ug/l
81703030 | Leachate well 3 | GU1 | O-Xylene | 15.6 | ug/l
81703030 | Leachate well 3 | GU2 | Styrene | <5.00 | ug/l
81703030 | Leachate well 3 | GU3 | Bromoform | <5.00 | ug/l
81703030 | Leachate well 3 | GU4 | iso-Propylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GU5 | 1,1,2,2-Tetrachloroethane | <5.00 | ug/l
81703030 | Leachate well 3 | GU6 | 1,2,3-Trichloropropane | <5.00 | ug/l
81703030 | Leachate well 3 | GU7 | Bromobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GU8 | n-propylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GU9 | 2-Chlorotoluene | <5.00 | ug/l
81703030 | Leachate well 3 | GUA | 1,3,5-Trimethylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUB | 4-Chlorotoluene | <5.00 | ug/l
81703030 | Leachate well 3 | GUC | tert-Butylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUD | 1,2,4-Trimethylbenzene | 16.2 | ug/l
81703030 | Leachate well 3 | GUE | sec-butylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUF | p-isopropyltoluene | 10.3 | ug/l
81703030 | Leachate well 3 | GUG | 1,3-Dichlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUH | 1,4-Dichlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUJ | n-butylbenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUK | 1,2-Dichlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUL | 1,2-Dibromo-3-chloropropane | <10.0 | ug/l
81703030 | Leachate well 3 | GUM | 1,2,4-Trichlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUN | Hexachlorobutadiene | <5.00 | ug/l
81703030 | Leachate well 3 | GUP | Naphthalene | 79.2 | ug/l
81703030 | Leachate well 3 | GUQ | 1,2,3-Trichlorobenzene | <5.00 | ug/l
81703030 | Leachate well 3 | GUR | Xylene (o+p+m) | 56.6 | ug/l
81703030 | Leachate well 3 | KKH | Tritium | 218 | Bq/l
81703030 | Leachate well 3 | V10 | SULPHATE AS SO4 | 265 | mg/l
81703030 | Leachate well 3 | V11 | CHLORIDE AS CL | 1790 | mg/l
81703040 | Leachate well 4 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703040 | Leachate well 4 | 0F4 | TOTAL ORGANIC CARBON | SEE A/C | mg/l | *Unable analyse for TOC due to insufficient sample.
81703040 | Leachate well 4 | 2 | pH | 8.4
81703040 | Leachate well 4 | 04Q | AMMONIACAL NITROGEN | 1960 | mg/l
81703040 | Leachate well 4 | 10 | BOD + ATU (5 DAY) | 7070 | mg/l
81703040 | Leachate well 4 | 16 | ALKALINITY AS CaCO3 | SEE A/C | mg/l | *Unable to analyse for Alkalinity due to insufficient sample.
81703040 | Leachate well 4 | 29 | CHROMIUM, TOTAL AS CR | SEE A/C | mg/l | *Unable to provide ICP-OES metals results due to insufficient sample.
81703040 | Leachate well 4 | 39 | CALCIUM TOTAL AS CA | SEE A/C | mg/l | *Unable to provide ICP-OES metals results due to insufficient sample.
81703040 | Leachate well 4 | 40 | MAGNESIUM AS MG | SEE A/C | mg/l | *Unable to provide ICP-OES metals results due to insufficient sample.
81703040 | Leachate well 4 | 41 | SODIUM AS NA | SEE A/C | mg/l | *Unable to provide ICP-OES metals results due to insufficient sample.
81703040 | Leachate well 4 | 42 | POTASSIUM AS K | SEE A/C | mg/l | *Unable to provide ICP-OES metals results due to insufficient sample.
81703040 | Leachate well 4 | 54 | ELECTRICAL CONDUCTIVITY | SEE A/C | uS/cm | *Unable to analyse for Electric conductivity due to insufficient sample.
81703040 | Leachate well 4 | 70 | CHEMICAL OXYGEN DEMAND | 12800 | mg/l
81703040 | Leachate well 4 | 70T | IRON, TOTAL AS FE | 16 | mg/l
81703040 | Leachate well 4 | 70V | MANGANESE AS MN | 0.66 | mg/l
81703040 | Leachate well 4 | 70Z | NICKEL TOTAL AS NI | 0.13 | mg/l
81703040 | Leachate well 4 | 716 | COPPER TOAL AS CU | 0.087 | mg/l
81703040 | Leachate well 4 | 719 | ZINC | 0.15 | mg/l
81703040 | Leachate well 4 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703040 | Leachate well 4 | 731 | LEAD TOTAL AS PB | 0.0044 | mg/l
81703040 | Leachate well 4 | CAA | SULPHATE AS SO4 | SEE A/C | mg/l | *Unable to analyse for Sulphate due to insufficient sample.
81703040 | Leachate well 4 | GED | BENTAZONE | <20.0 | ug/l
81703040 | Leachate well 4 | GFA | BROMOXYNIL | <20.0 | ug/l
81703040 | Leachate well 4 | GFW | 2,3,6-TBA | <20.0 | ug/l
81703040 | Leachate well 4 | GFY | 2,4-D | <20.0 | ug/l
81703040 | Leachate well 4 | GFZ | 2,4-DB | <20.0 | ug/l
81703040 | Leachate well 4 | GG3 | 2,4,5-T | <20.0 | ug/l
81703040 | Leachate well 4 | GG8 | MECOPROP | 51 | ug/l
81703040 | Leachate well 4 | GG9 | DICAMBA | <20.0 | ug/l
81703040 | Leachate well 4 | GGA | MCPA | <20.0 | ug/l
81703040 | Leachate well 4 | GGB | DICHLORPROP | <20.0 | ug/l
81703040 | Leachate well 4 | GGC | MCPB | <20.0 | ug/l
81703040 | Leachate well 4 | GGD | IOXYNIL | <20.0 | ug/l
81703040 | Leachate well 4 | GGE | CLOPYRALID | <20.0 | ug/l
81703040 | Leachate well 4 | GKW | BENAZOLIN | <20.0 | ug/l
81703040 | Leachate well 4 | GKX | FENOPROP | <20.0 | ug/l
81703040 | Leachate well 4 | GKY | TRICLOPYR | <20.0 | ug/l
81703040 | Leachate well 4 | GKZ | FLUROXYPYR | <20.0 | ug/l
81703040 | Leachate well 4 | GS3 | Dichlorodifluoromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GS4 | Chloromethane | <10.0 | ug/l
81703040 | Leachate well 4 | GS5 | Vinyl Chloride | <2.50 | ug/l
81703040 | Leachate well 4 | GS6 | Bromomethane | <5.00 | ug/l
81703040 | Leachate well 4 | GS7 | Chloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GS8 | Trichlorofluoromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GS9 | 1,1-Dichloroethene | <5.00 | ug/l
81703040 | Leachate well 4 | GSS | Dichloromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GSU | MTBE | <5.00 | ug/l
81703040 | Leachate well 4 | GSV | trans-1,2-Dichloroethene | <5.00 | ug/l
81703040 | Leachate well 4 | GSW | 1,1-Dichloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GSX | 1,2-Dichloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GSY | 2,2-Dichloropropane | <5.00 | ug/l
81703040 | Leachate well 4 | GSZ | Bromochloromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GT1 | Chloroform | <5.00 | ug/l
81703040 | Leachate well 4 | GT2 | 1,1,1-Trichloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GT6 | 1,1-Dichloropropene | <5.00 | ug/l
81703040 | Leachate well 4 | GT7 | Carbon Tetrachloride | <5.00 | ug/l
81703040 | Leachate well 4 | GT8 | 1,2-Dichloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GT9 | Benzene | 44.4 | ug/l
81703040 | Leachate well 4 | GTJ | Trichloroethene | <5.00 | ug/l
81703040 | Leachate well 4 | GTK | 1,2-Dichloropropane | <5.00 | ug/l
81703040 | Leachate well 4 | GTL | Dibromomethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTM | Bromodichloromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTN | cis-1,3-Dichloropropene | <5.00 | ug/l
81703040 | Leachate well 4 | GTP | Toluene | 46.1 | ug/l
81703040 | Leachate well 4 | GTQ | trans-1,3-Dichloropropene | <5.00 | ug/l
81703040 | Leachate well 4 | GTR | 1,1,2-Trichloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTT | Tetrachloroethene | <5.00 | ug/l
81703040 | Leachate well 4 | GTU | 1,3-Dichloropropane | <5.00 | ug/l
81703040 | Leachate well 4 | GTV | Dibromochloromethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTW | 1,2-Dibromoethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTX | Chlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GTY | 1,1,1,2-Tetrachloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GTZ | Ethyl Benzene | 14.4 | ug/l
81703040 | Leachate well 4 | GU0 | m and p-xylene | 20.1 | ug/l
81703040 | Leachate well 4 | GU1 | O-Xylene | 11.2 | ug/l
81703040 | Leachate well 4 | GU2 | Styrene | <5.00 | ug/l
81703040 | Leachate well 4 | GU3 | Bromoform | <5.00 | ug/l
81703040 | Leachate well 4 | GU4 | iso-Propylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GU5 | 1,1,2,2-Tetrachloroethane | <5.00 | ug/l
81703040 | Leachate well 4 | GU6 | 1,2,3-Trichloropropane | <5.00 | ug/l
81703040 | Leachate well 4 | GU7 | Bromobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GU8 | n-propylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GU9 | 2-Chlorotoluene | <5.00 | ug/l
81703040 | Leachate well 4 | GUA | 1,3,5-Trimethylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUB | 4-Chlorotoluene | <5.00 | ug/l
81703040 | Leachate well 4 | GUC | tert-Butylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUD | 1,2,4-Trimethylbenzene | 6.51 | ug/l
81703040 | Leachate well 4 | GUE | sec-butylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUF | p-isopropyltoluene | 7.43 | ug/l
81703040 | Leachate well 4 | GUG | 1,3-Dichlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUH | 1,4-Dichlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUJ | n-butylbenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUK | 1,2-Dichlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUL | 1,2-Dibromo-3-chloropropane | <10.0 | ug/l
81703040 | Leachate well 4 | GUM | 1,2,4-Trichlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUN | Hexachlorobutadiene | <5.00 | ug/l
81703040 | Leachate well 4 | GUP | Naphthalene | 174 | ug/l
81703040 | Leachate well 4 | GUQ | 1,2,3-Trichlorobenzene | <5.00 | ug/l
81703040 | Leachate well 4 | GUR | Xylene (o+p+m) | 31.2 | ug/l
81703040 | Leachate well 4 | KKH | Tritium | 782 | Bq/l
81703040 | Leachate well 4 | V11 | CHLORIDE AS CL | 5110 | mg/l
81703050 | leachate well 5 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703050 | leachate well 5 | 0F4 | TOTAL ORGANIC CARBON | 250 | mg/l
81703050 | leachate well 5 | 2 | pH | 7.6
81703050 | leachate well 5 | 04Q | AMMONIACAL NITROGEN | 684 | mg/l
81703050 | leachate well 5 | 10 | BOD + ATU (5 DAY) | 60 | mg/l
81703050 | leachate well 5 | 16 | ALKALINITY AS CaCO3 | 3620 | mg/l
81703050 | leachate well 5 | 29 | CHROMIUM, TOTAL AS CR | 0.057 | mg/l
81703050 | leachate well 5 | 39 | CALCIUM TOTAL AS CA | 84.2 | mg/l
81703050 | leachate well 5 | 40 | MAGNESIUM AS MG | 77.5 | mg/l
81703050 | leachate well 5 | 41 | SODIUM AS NA | 803 | mg/l
81703050 | leachate well 5 | 42 | POTASSIUM AS K | 349 | mg/l
81703050 | leachate well 5 | 54 | ELECTRICAL CONDUCTIVITY | 9710 | uS/cm
81703050 | leachate well 5 | 70 | CHEMICAL OXYGEN DEMAND | 1080 | mg/l
81703050 | leachate well 5 | 70T | IRON, TOTAL AS FE | 2.2 | mg/l
81703050 | leachate well 5 | 70V | MANGANESE AS MN | 0.32 | mg/l
81703050 | leachate well 5 | 70Z | NICKEL TOTAL AS NI | 0.18 | mg/l
81703050 | leachate well 5 | 716 | COPPER TOAL AS CU | 0.033 | mg/l
81703050 | leachate well 5 | 719 | ZINC | 0.13 | mg/l
81703050 | leachate well 5 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703050 | leachate well 5 | 731 | LEAD TOTAL AS PB | <0.0030 | mg/l
81703050 | leachate well 5 | GED | BENTAZONE | <1.00 | ug/l
81703050 | leachate well 5 | GFA | BROMOXYNIL | <1.00 | ug/l
81703050 | leachate well 5 | GFW | 2,3,6-TBA | <1.00 | ug/l
81703050 | leachate well 5 | GFY | 2,4-D | <1.00 | ug/l
81703050 | leachate well 5 | GFZ | 2,4-DB | <1.00 | ug/l
81703050 | leachate well 5 | GG3 | 2,4,5-T | <1.00 | ug/l
81703050 | leachate well 5 | GG8 | MECOPROP | 11.2 | ug/l
81703050 | leachate well 5 | GG9 | DICAMBA | <1.00 | ug/l
81703050 | leachate well 5 | GGA | MCPA | <1.00 | ug/l
81703050 | leachate well 5 | GGB | DICHLORPROP | <1.00 | ug/l
81703050 | leachate well 5 | GGC | MCPB | <1.00 | ug/l
81703050 | leachate well 5 | GGD | IOXYNIL | <1.00 | ug/l
81703050 | leachate well 5 | GGE | CLOPYRALID | <1.00 | ug/l
81703050 | leachate well 5 | GKW | BENAZOLIN | <1.00 | ug/l
81703050 | leachate well 5 | GKX | FENOPROP | <1.00 | ug/l
81703050 | leachate well 5 | GKY | TRICLOPYR | <1.00 | ug/l
81703050 | leachate well 5 | GKZ | FLUROXYPYR | <1.00 | ug/l
81703050 | leachate well 5 | GS3 | Dichlorodifluoromethane | <5.00 | ug/l
81703050 | leachate well 5 | GS4 | Chloromethane | <10.0 | ug/l
81703050 | leachate well 5 | GS5 | Vinyl Chloride | <2.50 | ug/l
81703050 | leachate well 5 | GS6 | Bromomethane | <5.00 | ug/l
81703050 | leachate well 5 | GS7 | Chloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GS8 | Trichlorofluoromethane | <5.00 | ug/l
81703050 | leachate well 5 | GS9 | 1,1-Dichloroethene | <5.00 | ug/l
81703050 | leachate well 5 | GSS | Dichloromethane | <5.00 | ug/l
81703050 | leachate well 5 | GSU | MTBE | <5.00 | ug/l
81703050 | leachate well 5 | GSV | trans-1,2-Dichloroethene | <5.00 | ug/l
81703050 | leachate well 5 | GSW | 1,1-Dichloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GSX | 1,2-Dichloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GSY | 2,2-Dichloropropane | <5.00 | ug/l
81703050 | leachate well 5 | GSZ | Bromochloromethane | <5.00 | ug/l
81703050 | leachate well 5 | GT1 | Chloroform | <5.00 | ug/l
81703050 | leachate well 5 | GT2 | 1,1,1-Trichloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GT6 | 1,1-Dichloropropene | <5.00 | ug/l
81703050 | leachate well 5 | GT7 | Carbon Tetrachloride | <5.00 | ug/l
81703050 | leachate well 5 | GT8 | 1,2-Dichloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GT9 | Benzene | 10.7 | ug/l
81703050 | leachate well 5 | GTJ | Trichloroethene | <5.00 | ug/l
81703050 | leachate well 5 | GTK | 1,2-Dichloropropane | <5.00 | ug/l
81703050 | leachate well 5 | GTL | Dibromomethane | <5.00 | ug/l
81703050 | leachate well 5 | GTM | Bromodichloromethane | <5.00 | ug/l
81703050 | leachate well 5 | GTN | cis-1,3-Dichloropropene | <5.00 | ug/l
81703050 | leachate well 5 | GTP | Toluene | 9.84 | ug/l
81703050 | leachate well 5 | GTQ | trans-1,3-Dichloropropene | <5.00 | ug/l
81703050 | leachate well 5 | GTR | 1,1,2-Trichloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GTT | Tetrachloroethene | <5.00 | ug/l
81703050 | leachate well 5 | GTU | 1,3-Dichloropropane | <5.00 | ug/l
81703050 | leachate well 5 | GTV | Dibromochloromethane | <5.00 | ug/l
81703050 | leachate well 5 | GTW | 1,2-Dibromoethane | <5.00 | ug/l
81703050 | leachate well 5 | GTX | Chlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GTY | 1,1,1,2-Tetrachloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GTZ | Ethyl Benzene | 32.6 | ug/l
81703050 | leachate well 5 | GU0 | m and p-xylene | 29 | ug/l
81703050 | leachate well 5 | GU1 | O-Xylene | 10.9 | ug/l
81703050 | leachate well 5 | GU2 | Styrene | <5.00 | ug/l
81703050 | leachate well 5 | GU3 | Bromoform | <5.00 | ug/l
81703050 | leachate well 5 | GU4 | iso-Propylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GU5 | 1,1,2,2-Tetrachloroethane | <5.00 | ug/l
81703050 | leachate well 5 | GU6 | 1,2,3-Trichloropropane | <5.00 | ug/l
81703050 | leachate well 5 | GU7 | Bromobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GU8 | n-propylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GU9 | 2-Chlorotoluene | <5.00 | ug/l
81703050 | leachate well 5 | GUA | 1,3,5-Trimethylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUB | 4-Chlorotoluene | <5.00 | ug/l
81703050 | leachate well 5 | GUC | tert-Butylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUD | 1,2,4-Trimethylbenzene | 14.8 | ug/l
81703050 | leachate well 5 | GUE | sec-butylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUF | p-isopropyltoluene | <5.00 | ug/l
81703050 | leachate well 5 | GUG | 1,3-Dichlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUH | 1,4-Dichlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUJ | n-butylbenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUK | 1,2-Dichlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUL | 1,2-Dibromo-3-chloropropane | <10.0 | ug/l
81703050 | leachate well 5 | GUM | 1,2,4-Trichlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUN | Hexachlorobutadiene | <5.00 | ug/l
81703050 | leachate well 5 | GUP | Naphthalene | 33.6 | ug/l
81703050 | leachate well 5 | GUQ | 1,2,3-Trichlorobenzene | <5.00 | ug/l
81703050 | leachate well 5 | GUR | Xylene (o+p+m) | 39.8 | ug/l
81703050 | leachate well 5 | KKH | Tritium | 735 | Bq/l
81703050 | leachate well 5 | V10 | SULPHATE AS SO4 | <4.4 | mg/l
81703050 | leachate well 5 | V11 | CHLORIDE AS CL | 1340 | mg/l
81703060 | leachate well 6 | 0A0 | NITROGEN TOTAL OXIDISED AS N | <0.7 | mg/l
81703060 | leachate well 6 | 0F4 | TOTAL ORGANIC CARBON | 2760 | mg/l
81703060 | leachate well 6 | 2 | pH | 7.9
81703060 | leachate well 6 | 04Q | AMMONIACAL NITROGEN | 2510 | mg/l
81703060 | leachate well 6 | 10 | BOD + ATU (5 DAY) | 2960 | mg/l
81703060 | leachate well 6 | 16 | ALKALINITY AS CaCO3 | 8580 | mg/l
81703060 | leachate well 6 | 29 | CHROMIUM, TOTAL AS CR | 0.136 | mg/l
81703060 | leachate well 6 | 39 | CALCIUM TOTAL AS CA | 62.9 | mg/l
81703060 | leachate well 6 | 40 | MAGNESIUM AS MG | 101 | mg/l
81703060 | leachate well 6 | 41 | SODIUM AS NA | 2630 | mg/l
81703060 | leachate well 6 | 42 | POTASSIUM AS K | 974 | mg/l
81703060 | leachate well 6 | 54 | ELECTRICAL CONDUCTIVITY | 31000 | uS/cm
81703060 | leachate well 6 | 70 | CHEMICAL OXYGEN DEMAND | 8710 | mg/l
81703060 | leachate well 6 | 70T | IRON, TOTAL AS FE | 2.2 | mg/l
81703060 | leachate well 6 | 70V | MANGANESE AS MN | 0.1 | mg/l
81703060 | leachate well 6 | 70Z | NICKEL TOTAL AS NI | 0.23 | mg/l
81703060 | leachate well 6 | 716 | COPPER TOAL AS CU | 0.18 | mg/l
81703060 | leachate well 6 | 719 | ZINC | 0.86 | mg/l
81703060 | leachate well 6 | 725 | CADMIUM, TOTAL AS CD | <0.00070 | mg/l
81703060 | leachate well 6 | 731 | LEAD TOTAL AS PB | 0.028 | mg/l
81703060 | leachate well 6 | CAA | SULPHATE AS SO4 | 23.8 | mg/l
81703060 | leachate well 6 | GED | BENTAZONE | <20.0 | ug/l
81703060 | leachate well 6 | GFA | BROMOXYNIL | <20.0 | ug/l
81703060 | leachate well 6 | GFW | 2,3,6-TBA | <20.0 | ug/l
81703060 | leachate well 6 | GFY | 2,4-D | <20.0 | ug/l
81703060 | leachate well 6 | GFZ | 2,4-DB | <20.0 | ug/l
81703060 | leachate well 6 | GG3 | 2,4,5-T | <20.0 | ug/l
81703060 | leachate well 6 | GG8 | MECOPROP | 81.5 | ug/l
81703060 | leachate well 6 | GG9 | DICAMBA | <20.0 | ug/l
81703060 | leachate well 6 | GGA | MCPA | <20.0 | ug/l
81703060 | leachate well 6 | GGB | DICHLORPROP | 66.8 | ug/l
81703060 | leachate well 6 | GGC | MCPB | <20.0 | ug/l
81703060 | leachate well 6 | GGD | IOXYNIL | <20.0 | ug/l
81703060 | leachate well 6 | GGE | CLOPYRALID | <20.0 | ug/l
81703060 | leachate well 6 | GKW | BENAZOLIN | <20.0 | ug/l
81703060 | leachate well 6 | GKX | FENOPROP | <20.0 | ug/l
81703060 | leachate well 6 | GKY | TRICLOPYR | <20.0 | ug/l
81703060 | leachate well 6 | GKZ | FLUROXYPYR | <20.0 | ug/l
81703060 | leachate well 6 | GS3 | Dichlorodifluoromethane | <5.00 | ug/l
81703060 | leachate well 6 | GS4 | Chloromethane | <10.0 | ug/l
81703060 | leachate well 6 | GS5 | Vinyl Chloride | <2.50 | ug/l
81703060 | leachate well 6 | GS6 | Bromomethane | <5.00 | ug/l
81703060 | leachate well 6 | GS7 | Chloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GS8 | Trichlorofluoromethane | <5.00 | ug/l
81703060 | leachate well 6 | GS9 | 1,1-Dichloroethene | <5.00 | ug/l
81703060 | leachate well 6 | GSS | Dichloromethane | <5.00 | ug/l
81703060 | leachate well 6 | GSU | MTBE | <5.00 | ug/l
81703060 | leachate well 6 | GSV | trans-1,2-Dichloroethene | <5.00 | ug/l
81703060 | leachate well 6 | GSW | 1,1-Dichloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GSX | 1,2-Dichloroethane | 9.93 | ug/l
81703060 | leachate well 6 | GSY | 2,2-Dichloropropane | <5.00 | ug/l
81703060 | leachate well 6 | GSZ | Bromochloromethane | <5.00 | ug/l
81703060 | leachate well 6 | GT1 | Chloroform | <5.00 | ug/l
81703060 | leachate well 6 | GT2 | 1,1,1-Trichloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GT6 | 1,1-Dichloropropene | <5.00 | ug/l
81703060 | leachate well 6 | GT7 | Carbon Tetrachloride | <5.00 | ug/l
81703060 | leachate well 6 | GT8 | 1,2-Dichloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GT9 | Benzene | 9.24 | ug/l
81703060 | leachate well 6 | GTJ | Trichloroethene | <5.00 | ug/l
81703060 | leachate well 6 | GTK | 1,2-Dichloropropane | <5.00 | ug/l
81703060 | leachate well 6 | GTL | Dibromomethane | <5.00 | ug/l
81703060 | leachate well 6 | GTM | Bromodichloromethane | <5.00 | ug/l
81703060 | leachate well 6 | GTN | cis-1,3-Dichloropropene | <5.00 | ug/l
81703060 | leachate well 6 | GTP | Toluene | 30.1 | ug/l
81703060 | leachate well 6 | GTQ | trans-1,3-Dichloropropene | <5.00 | ug/l
81703060 | leachate well 6 | GTR | 1,1,2-Trichloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GTT | Tetrachloroethene | <5.00 | ug/l
81703060 | leachate well 6 | GTU | 1,3-Dichloropropane | <5.00 | ug/l
81703060 | leachate well 6 | GTV | Dibromochloromethane | <5.00 | ug/l
81703060 | leachate well 6 | GTW | 1,2-Dibromoethane | <5.00 | ug/l
81703060 | leachate well 6 | GTX | Chlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GTY | 1,1,1,2-Tetrachloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GTZ | Ethyl Benzene | 18 | ug/l
81703060 | leachate well 6 | GU0 | m and p-xylene | 33.4 | ug/l
81703060 | leachate well 6 | GU1 | O-Xylene | 12.5 | ug/l
81703060 | leachate well 6 | GU2 | Styrene | <5.00 | ug/l
81703060 | leachate well 6 | GU3 | Bromoform | <5.00 | ug/l
81703060 | leachate well 6 | GU4 | iso-Propylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GU5 | 1,1,2,2-Tetrachloroethane | <5.00 | ug/l
81703060 | leachate well 6 | GU6 | 1,2,3-Trichloropropane | <5.00 | ug/l
81703060 | leachate well 6 | GU7 | Bromobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GU8 | n-propylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GU9 | 2-Chlorotoluene | <5.00 | ug/l
81703060 | leachate well 6 | GUA | 1,3,5-Trimethylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUB | 4-Chlorotoluene | <5.00 | ug/l
81703060 | leachate well 6 | GUC | tert-Butylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUD | 1,2,4-Trimethylbenzene | 11.7 | ug/l
81703060 | leachate well 6 | GUE | sec-butylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUF | p-isopropyltoluene | 7.41 | ug/l
81703060 | leachate well 6 | GUG | 1,3-Dichlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUH | 1,4-Dichlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUJ | n-butylbenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUK | 1,2-Dichlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUL | 1,2-Dibromo-3-chloropropane | <10.0 | ug/l
81703060 | leachate well 6 | GUM | 1,2,4-Trichlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUN | Hexachlorobutadiene | <5.00 | ug/l
81703060 | leachate well 6 | GUP | Naphthalene | 12.1 | ug/l
81703060 | leachate well 6 | GUQ | 1,2,3-Trichlorobenzene | <5.00 | ug/l
81703060 | leachate well 6 | GUR | Xylene (o+p+m) | 45.9 | ug/l
81703060 | leachate well 6 | KKH | Tritium | 76 | Bq/l
81703060 | leachate well 6 | V11 | CHLORIDE AS CL | 6540 | mg/l

## Leachate Treatment Plant
Sample | Sample_Description | Code | Description | 2021-01-28 | 2021-02-17 | 2021-03-31 | Unit
81703400 | Leachate Sewer Discharge | 2 | pH | 7.4 | 7 | 6.9
81703400 | Leachate Sewer Discharge | 7 | Suspended Solids | SEE A/C | 93 | 21 | mg/l | *Unable to obtain a confirming result for total suspended solids
81703400 | Leachate Sewer Discharge | 09Z | Cyanide, total as CN | 0.043 | 0.034 | 0.029 | mg/l
81703400 | Leachate Sewer Discharge | 10 | BOD + ATU (5 DAY) | 11 | 20 | 9 | mg/l
81703400 | Leachate Sewer Discharge | 17 | AMMONIACAL NITROGEN AS N | 0.44 | <0.41 | 1.16 | mg/l
81703400 | Leachate Sewer Discharge | 29 | CHROMIUM, TOTAL AS CR | 0.125 | 0.115 | 0.125 | mg/l
81703400 | Leachate Sewer Discharge | 54 | ELECTRICAL CONDUCTIVITY | 14100 | 12800 | 14300 | uS/cm
81703400 | Leachate Sewer Discharge | 59 | SULPHIDE AS S | <0.020 | 0.025 | <0.020 | mg/l
81703400 | Leachate Sewer Discharge | 65 | SILVER | <0.0007 | <0.0007 | <0.0007 | mg/l
81703400 | Leachate Sewer Discharge | 70 | CHEMICAL OXYGEN DEMAND | 852 | 767 | 831 | mg/l
81703400 | Leachate Sewer Discharge | 70M | TITANIUM | 0.031 | 0.024 | 0.024 | mg/l
81703400 | Leachate Sewer Discharge | 70P | VANADIUM | 0.03 | 0.027 | 0.037 | mg/l
81703400 | Leachate Sewer Discharge | 70X | COBOLT TOTAL AS CO | 0.023 | 0.022 | 0.025 | mg/l
81703400 | Leachate Sewer Discharge | 70Z | NICKEL TOTAL AS NI | 0.14 | 0.13 | 0.15 | mg/l
81703400 | Leachate Sewer Discharge | 71S | Arsenic, total as As | 0.061 | 0.056 | 0.076 | mg/l
81703400 | Leachate Sewer Discharge | 71U | SELENIUM | <0.0060 | <0.0060 | <0.0060 | mg/l
81703400 | Leachate Sewer Discharge | 101 | TEMPERATURE | 21.4 | 21.7 | 24.8 | DegC
81703400 | Leachate Sewer Discharge | 302 | DISSOLVED METHANE | <0.010 | <0.010 | <0.010 | mg/l
81703400 | Leachate Sewer Discharge | 705 | BERYLLIUM, TOTAL AS BE | <0.0060 | <0.0060 | <0.0060 | mg/l
81703400 | Leachate Sewer Discharge | 716 | COPPER TOAL AS CU | <0.018 | <0.018 | <0.018 | mg/l
81703400 | Leachate Sewer Discharge | 719 | ZINC | 0.12 | 0.091 | 0.093 | mg/l
81703400 | Leachate Sewer Discharge | 723 | MOLYBDENUM | <0.027 | <0.027 | <0.027 | mg/l
81703400 | Leachate Sewer Discharge | 725 | CADMIUM, TOTAL AS CD | <0.00070 | <0.00070 | <0.00070 | mg/l
81703400 | Leachate Sewer Discharge | 727 | TIN | <0.015 | <0.015 | <0.015 | mg/l
81703400 | Leachate Sewer Discharge | 729 | ANTIMONY | <0.016 | <0.016 | <0.016 | mg/l
81703400 | Leachate Sewer Discharge | 731 | LEAD TOTAL AS PB | <0.0030 | <0.0030 | <0.0030 | mg/l
81703400 | Leachate Sewer Discharge | G0F | EH C6-C40 | 222 | 275 | 291 | ug/l
81703400 | Leachate Sewer Discharge | GN9 | EH C6-C8 | <200 | <40 | <40 | ug/l
81703400 | Leachate Sewer Discharge | GQ1 | EH C8-C10 | <200 | <40 | <40 | ug/l
81703400 | Leachate Sewer Discharge | GQ2 | EH C10-C16 | 222 | 230 | 243 | ug/l
81703400 | Leachate Sewer Discharge | GQ3 | EH C16-C24 | <200 | 46 | 49 | ug/l
81703400 | Leachate Sewer Discharge | GQ4 | EH C24-C40 | <200 | <40 | <40 | ug/l
81703400 | Leachate Sewer Discharge | V10 | SULPHATE AS SO4 | 83.4 | 157 | 101 | mg/l
81703400 | Leachate Sewer Discharge | V11 | CHLORIDE AS CL | 2690 | 2620 | 2800 | mg/l
|  |  |  | 0.408 | 0.391 | 0.588
|  |  |  | 14973.93 | 13589.19 | 15156.33

## Ambient Air Monitoring
Date | Atmospheric Pressure | Rising/Falling | Cloud Cover | Sample Point | Odour Intensity | Odour Extent | Odour Description | Flam Gas Steady (ppmv) | Flam Gas Max (ppmv)
2021-01-22 | 992 | RISING | 80% | 81707001 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707002 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707003 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707004 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707005 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707006 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707007 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707008 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707009 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81707010 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907011 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907012 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907013 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907014 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907015 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907016 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907017 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907018 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907019 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907020 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907021 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907022 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907023 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907024 | 0 | 0 | 0 | 0 | 0
2021-01-22 | 992 | RISING | 80% | 81907025 | 2 | 1 | 2 | 20 | 35
2021-01-22 | 992 | RISING | 80% | 81907026 | 2 | 1 | 2 | 15 | 30
2021-01-22 | 992 | RISING | 80% | 81907027 | 2 | 1 | 2 | 15 | 30
2021-02-22 | 1014 | RISING | 80% | 81707001 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707002 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707003 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707004 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707005 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707006 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81707007 | 1 | 1 | 6 | 2 | 3
2021-02-22 | 1014 | RISING | 80% | 81707008 | 1 | 1 | 6 | 5 | 7
2021-02-22 | 1014 | RISING | 80% | 81707009 | 1 | 1 | 6 | 8 | 10
2021-02-22 | 1014 | RISING | 80% | 81707010 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907011 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907012 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907013 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907014 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907015 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907016 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907017 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907018 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907019 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907020 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907021 | 0 | 0 | 0 | 0 | 0
2021-02-22 | 1014 | RISING | 80% | 81907022 | 1 | 1 | 2 | 10 | 20
2021-02-22 | 1014 | RISING | 80% | 81907023 | 1 | 1 | 2 | 10 | 15
2021-02-22 | 1014 | RISING | 80% | 81907024 | 1 | 1 | 2 | 10 | 20
2021-02-22 | 1014 | RISING | 80% | 81907025 | 0 | 0 | 0 | 3 | 3
2021-02-22 | 1014 | RISING | 80% | 81907026 | 0 | 0 | 0 | 3 | 4
2021-02-22 | 1014 | RISING | 80% | 81907027 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707001 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707002 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707003 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707004 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707005 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707006 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707007 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707008 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707009 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81707010 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907011 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907012 | 2 | 1 | 2 | 15 | 25
2021-03-02 | 1029 | FALLING | 100% | 81907013 | 2 | 1 | 2 | 20 | 30
2021-03-02 | 1029 | FALLING | 100% | 81907014 | 2 | 1 | 2 | 20 | 30
2021-03-02 | 1029 | FALLING | 100% | 81907015 | 2 | 1 | 2 | 10 | 15
2021-03-02 | 1029 | FALLING | 100% | 81907016 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907017 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907018 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907019 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907020 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907021 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907022 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907023 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907024 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907025 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907026 | 0 | 0 | 0 | 0 | 0
2021-03-02 | 1029 | FALLING | 100% | 81907027 | 0 | 0 | 0 | 0 | 0

## Gas Compound
Date readings taken | Suction pressure mb | CH4 % | CO2 % | O2 % | Bal % | Flow m3/phr | Flare 1 Temp oC | Flare 2 Temp oC | Flare 3 Temp oC | CH4% | CO2% | O2%
| Uniflare | [8 empty] | Uniflare Fixed analyser
2021-01-04 | -174 | 41.7 | 29.8 | 3.7 | 24.8 | 1700 | PILOT 56 | PILOT 111 | PILOT 85 | 43.6 | 32.1 | 1.41
2021-01-11 | -107 | 46.6 | 32.6 | 2.3 | 18.5 | 1704 | PILOT 52 | PILOT 111 | PILOT 109 | 43.6 | 32.1 | 1.19
2021-01-15 | -133 | 48.8 | 33.1 | 1.8 | 16.3 | 1701 | PILOT 97 | PILOT 101 | PILOT 100 | 45.3 | 32.8 | 0.69
2021-01-18 | -135 | 50.1 | 33.5 | 1.5 | 14.9 | 1700 | pilot 87 | pilot 137 | pilot 102 | 45.5 | 32.9 | 0.69
2021-01-22 | -178 | 47.4 | 34 | 1.8 | 16.7 | 1700 | pilot 93 | pilot 124 | pilot 82 | 45.8 | 33.5 | 0.69
2021-01-25 | -226 | 44.6 | 33.9 | 1.4 | 20.1 | 1702 | pilot 72 | pilot 165 | pilot 55 | 44.7 | 33.1 | 0.85
2021-01-29 | -159 | 46.7 | 33.4 | 2 | 17.9 | 1701 | pilot 63 | pilot 128 | pilot 106 | 44.7 | 32.7 | 1.41
2021-02-01 | -197 | 45.1 | 34 | 1.6 | 19.3 | 1701 | pilot 79 | pilot 108 | pilot 69 | 44.8 | 33 | 1.02
2021-02-05 | -148 | 47.4 | 33.1 | 2 | 17.5 | 1705 | pilot 96 | pilot 121 | pilot 73 | 46.5 | 33.7 | 0.71
2021-02-08 | -180 | 44.7 | 33.7 | 1.8 | 19.8 | 1700 | pilot 47 | pilot 101 | pilot 77 | 44.7 | 32.9 | 1.25
2021-02-11 | -195 | 41.4 | 32.1 | 2.1 | 24.5 | 1702 | pilot 19 | pilot 94 | pilot 31 | 41.5 | 31.4 | 1.64
2021-02-15 | -178 | 45.9 | 33.2 | 1.4 | 19.4 | 1705 | pilot 82 | pilot 126 | pilot 86 | 44.1 | 32.4 | 0.69
2021-02-18 | -156 | 47.8 | 34.5 | 1.8 | 15.9 | 1702 | pilot 101 | pilot 112 | pilot 103 | 45.7 | 33.1 | 1.35
2021-02-22 | -144 | 46.7 | 32.8 | 2.1 | 18.4 | 1700 | pilot 96 | pilot 136 | pilot 101 | 45.9 | 32.8 | 1.42
2021-02-26 | -176 | 43.3 | 30.6 | 2.8 | 23.4 | 1704 | pilot 94 | pilot 122 | pilot 55 | 43.2 | 31.5 | 1.59
2021-03-02 | -200 | 42.9 | 33.4 | 1.4 | 22.3 | 1702 | pilot 64 | pilot 104 | pilot 54 | 43.6 | 32.7 | 0.79
2021-03-05 | -192 | 43.3 | 33.2 | 1.5 | 22 | 1702 | pilot 58 | pilot 99 | pilot 40 | 44.1 | 32.7 | 1.13
2021-03-08 | -206 | 44.1 | 33.7 | 1.4 | 20.9 | 1700 | pilot 90 | pilot 141 | pilot 48 | 45.1 | 33.2 | 0.85
2021-03-11 | -217 | 48.4 | 33.9 | 1.8 | 15.8 | 1703 | pilot 64 | pilot 103 | pilot 42 | 45.3 | 33.3 | 1.25
2021-03-15 | -178 | 42 | 29 | 3 | 26 | 1700 | pilot 82 | pilot 113 | pilot 60 | 41.3 | 31 | 1.63
2021-03-19 | -150 | 41.6 | 30.3 | 3.4 | 24.7 | 1405 | pilot 85 | pilot 117 | pilot 39 | 42.6 | 31.5 | 1.37
2021-03-22 | -218 | 43.5 | 31.1 | 3.4 | 22 | 1702 | pilot 95 | pilot 95 | pilot 41 | 44.4 | 32.8 | 1.2
2021-03-26 | -192 | 51 | 33.8 | 2 | 13.2 | 1603 | pilot 55 | pilot 131 | pilot 52 | 48.1 | 33.7 | 1.45
2021-03-29 | -189 | 46.3 | 32.1 | 3 | 18.6 | 1600 | pilot 86 | pilot 140 | pilot 63 | 46.5 | 33.1 | 1.42

## In-waste gas
Borehole | Description | Date | Time | CH4 | CO2 | O2 | CO | H2S | Bal | Atmos | Relative | Flow | Valve or KO Pot Hours | Anemometer | Well Condition | Reas | Reason | Actioned | Wind Speed | Ground Conditions | Precipitation | Cloud Cover | Wind Direction
TR000GW2 | gas well 2 | 2021-01-04 | 15:02 | 55.3 | 21.7 | 4.1 | 14 | 0 | 18.9 | 972 | -22.44 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW2 | gas well 2 | 2021-01-15 | 9:38 | 65.8 | 23.6 | 3.2 | 17 | 18 | 7.4 | 982 | -12.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW2 | gas well 2 | 2021-01-22 | 10:00 | 55.1 | 21.2 | 5.5 | 16 | 15 | 18.2 | 946 | -20.58 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW2 | gas well 2 | 2021-01-27 | 10:36 | 47.1 | 18.3 | 7.1 | 9 | 4 | 27.5 | 967 | -16.94 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW2 | gas well 2 | 2021-02-05 | 13:44 | 57.6 | 22.1 | 4 | 6 | 11 | 16.3 | 959 | -19.65 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW2 | gas well 2 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW2 | gas well 2 | 2021-02-16 | 11:18 | 28.7 | 11.7 | 11.8 | 3 | 0 | 47.8 | 960 | -73.08 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW2 | gas well 2 | 2021-02-26 | 12:47 | 52.2 | 18.6 | 5.4 | 0 | 1 | 23.8 | 991 | -49.74 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW2 | gas well 2 | 2021-03-03 | 14:11 | 48.6 | 18.4 | 4.8 | 0 | 0 | 28.2 | 979 | -49.88 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW2 | gas well 2 | 2021-03-09 | 10:14 | 76.5 | 25.9 | 0.4 | 18 | 9 | 0 | 973 | 21.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW2 | gas well 2 | 2021-03-16 | 14:02 | 24.2 | 9.2 | 12.8 | 19 | 11 | 53.8 | 982 | -92.95 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW2 | gas well 2 | 2021-03-25 | 14:28 | 71.5 | 25.7 | 0.4 | 21 | 18 | 2.4 | 969 | -4.37 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW2 | gas well 2 | 2021-03-30 | 14:18 | 35 | 13.5 | 8.6 | 28 | 12 | 42.9 | 981 | -90.23 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-01-04 | 15:03 | 77.7 | 26.4 | 0.5 | 15 | 5 | 0 | 973 | -3.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-01-04 | 15:04 | 78.7 | 27 | 0 | 15 | 6 | 0 | 973 | -7.38 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-01-15 | 9:39 | 40.2 | 27.3 | 0.1 | 16 | 7 | 32.4 | 982 | -10.53 |  | 10 |  | Investigation/attention required |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW3 | gas well 3 | 2021-01-15 | 9:39 | 39.1 | 27.2 | 0 | 16 | 6 | 33.7 | 982 | -4.84 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW3 | gas well 3 | 2021-01-22 | 10:01 | 55.4 | 20.7 | 6.2 | 15 | 6 | 17.7 | 947 | -5.05 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW3 | gas well 3 | 2021-01-27 | 10:35 | 72.1 | 27 | 0.4 | 14 | 42 | 0.5 | 966 | -3.3 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-02-05 | 13:45 | 76.2 | 25.3 | 0.6 | 5 | 2 | 0 | 960 | -2.52 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW3 | gas well 3 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-02-16 | 11:16 | 53.4 | 19.6 | 5.6 | 9 | 21 | 21.4 | 960 | -2.39 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW3 | gas well 3 | 2021-02-26 | 12:48 | 35.1 | 12.2 | 10.6 | 0 | 0 | 42.1 | 991 | -1.98 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW3 | gas well 3 | 2021-03-03 | 14:12 | 40 | 14.3 | 9.2 | 0 | 0 | 36.5 | 979 | -0.61 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW3 | gas well 3 | 2021-03-09 | 10:16 | 35 | 12.5 | 10.7 | 13 | 2 | 41.8 | 974 | -3.96 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW3 | gas well 3 | 2021-03-16 | 14:03 | 32.7 | 11.8 | 11.4 | 17 | 4 | 44.1 | 982 | -3.92 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW3 | gas well 3 | 2021-03-25 | 14:29 | 47.6 | 17.1 | 7.5 | 19 | 5 | 27.8 | 970 | -2.66 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW3 | gas well 3 | 2021-03-30 | 14:19 | 35.1 | 12.6 | 10.1 | 25 | 7 | 42.2 | 981 | -2.67 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW4 | gas well 4 | 2021-01-04 | 15:06 | 53.3 | 34.9 | 0.3 | 16 | 46 | 11.5 | 972 | -4.13 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW4 | gas well 4 | 2021-01-15 | 9:41 | 57.2 | 35 | 0.4 | 18 | 51 | 7.4 | 982 | -4.3 |  | 20 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW4 | gas well 4 | 2021-01-22 | 10:02 | 56 | 35.2 | 0.8 | 18 | 55 | 8 | 946 | -8.16 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW4 | gas well 4 | 2021-01-27 | 10:33 | 49.8 | 34.4 | 0.3 | 17 | 82 | 15.5 | 965 | -3.3 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW4 | gas well 4 | 2021-02-05 | 13:46 | 52.5 | 35.1 | 0.2 | 8 | 86 | 12.2 | 960 | -1.7 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW4 | gas well 4 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW4 | gas well 4 | 2021-02-16 | 11:15 | 49.8 | 35 | 0.8 | 11 | 67 | 14.4 | 959 | -4.41 |  | 20 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW4 | gas well 4 | 2021-02-26 | 12:50 | 46.1 | 31.3 | 0.2 | 4 | 49 | 22.4 | 991 | -4.2 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW4 | gas well 4 | 2021-03-03 | 14:14 | 45 | 30.8 | 0.3 | 2 | 44 | 23.9 | 979 | -0.8 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW4 | gas well 4 | 2021-03-09 | 10:17 | 44.1 | 32.1 | 0.1 | 18 | 76 | 23.7 | 973 | -4.08 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW4 | gas well 4 | 2021-03-16 | 14:05 | 43 | 31.3 | 0.2 | 24 | 79 | 25.5 | 982 | -4.25 |  | 20 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW4 | gas well 4 | 2021-03-25 | 14:30 | 47.4 | 31.8 | 0.2 | 22 | 67 | 20.6 | 970 | -2.46 |  | 20 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW4 | gas well 4 | 2021-03-30 | 14:21 | 47 | 31.9 | 0.1 | 33 | 78 | 21 | 981 | -0.24 |  | 20 |  | Odour/migration control |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-01-04 | 15:00 | 72.9 | 27.5 | 0 | 15 | 0 | 0 | 973 | -17.3 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-01-04 | 15:00 | 71.3 | 26.7 | 0.6 | 17 | 1 | 1.4 | 973 | -1.18 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-01-15 | 9:36 | 74.4 | 28.8 | 0.3 | 20 | 33 | 0 | 983 | -20.04 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW5 | gas well 5 | 2021-01-22 | 9:58 | 77.8 | 29.9 | 0.1 | 19 | 48 | 0 | 946 | -190.3 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-01-22 | 9:58 | 76.6 | 29.7 | 0.8 | 20 | 39 | 0 | 946 | -151.21 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-01-27 | 10:38 | 70.3 | 27.2 | 0.9 | 9 | 26 | 1.6 | 966 | -138.44 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-02-05 | 13:42 | 72.8 | 27.1 | 0.3 | 10 | 21 | 0 | 959 | -103.52 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-02-16 | 11:20 | 75.5 | 27.2 | 0.9 | 6 | 20 | 0 | 961 | -165.74 |  | 20 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-02-26 | 12:46 | 73 | 25.4 | 0.4 | 6 | 2 | 1.2 | 991 | -172.92 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-03-03 | 14:10 | 71.8 | 25.8 | 0.5 | 3 | 5 | 1.9 | 979 | -181.53 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW5 | gas well 5 | 2021-03-09 | 10:13 | 76 | 26.5 | 0.7 | 19 | 8 | 0 | 974 | -203.24 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW5 | gas well 5 | 2021-03-16 | 14:00 | 75 | 26.1 | 0.3 | 24 | 23 | 0 | 974 | -188.02 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW5 | gas well 5 | 2021-03-25 | 14:25 | 72.2 | 27.8 | 0.6 | 24 | 21 | 0 | 970 | -183.81 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-03-25 | 14:26 | 72.8 | 26.8 | 0.2 | 23 | 40 | 0.2 | 970 | -184.07 |  | 40 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW5 | gas well 5 | 2021-03-30 | 14:17 | 65.2 | 24.7 | 0.5 | 34 | 18 | 9.6 | 981 | -173.74 |  | 40 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW6 | gas well 6 | 2021-01-04 | 14:58 | 53.6 | 26.9 | 2.1 | 23 | 7 | 17.4 | 972 | -6.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW6 | gas well 6 | 2021-01-15 | 9:35 | 47.9 | 24.6 | 3 | 25 | 5 | 24.5 | 982 | -6.35 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW6 | gas well 6 | 2021-01-22 | 9:56 | 51 | 26.1 | 2.4 | 23 | 8 | 20.5 | 946 | -9.01 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW6 | gas well 6 | 2021-01-27 | 10:39 | 44.5 | 23.7 | 3.2 | 8 | 6 | 28.6 | 966 | -6.87 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW6 | gas well 6 | 2021-02-05 | 13:41 | 51.5 | 25.7 | 2.3 | 16 | 3 | 20.5 | 959 | -5.24 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW6 | gas well 6 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW6 | gas well 6 | 2021-02-16 | 11:21 | 57.4 | 26.3 | 1.3 | 6 | 5 | 15 | 960 | -5.19 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW6 | gas well 6 | 2021-02-26 | 12:44 | 49 | 23.8 | 2.4 | 11 | 0 | 24.8 | 991 | -7.01 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW6 | gas well 6 | 2021-03-03 | 14:08 | 43.3 | 21.5 | 4.4 | 6 | 0 | 30.8 | 979 | -5.9 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW6 | gas well 6 | 2021-03-09 | 10:11 | 40.4 | 20.1 | 5.8 | 23 | 4 | 33.7 | 973 | -6.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW6 | gas well 6 | 2021-03-16 | 13:59 | 37.1 | 17.9 | 7.6 | 28 | 7 | 37.4 | 983 | -7.5 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW6 | gas well 6 | 2021-03-25 | 14:24 | 43 | 21.2 | 5 | 28 | 7 | 30.8 | 970 | -3.73 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW6 | gas well 6 | 2021-03-30 | 14:15 | 38 | 17.9 | 6.3 | 42 | 9 | 37.8 | 981 | -4.7 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW7 | gas well 7 | 2021-01-04 | 14:57 | 58.2 | 38.7 | 0.1 | 27 | 12 | 3 | 972 | -16.52 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW7 | gas well 7 | 2021-01-15 | 9:33 | 60.9 | 38.6 | 0.5 | 30 | 12 | 0 | 982 | -21.42 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW7 | gas well 7 | 2021-01-22 | 9:55 | 61.5 | 39.5 | 0.3 | 27 | 18 | 0 | 946 | -29.36 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW7 | gas well 7 | 2021-01-27 | 10:41 | 53.9 | 37.1 | 0.3 | 12 | 11 | 8.7 | 966 | -20.11 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW7 | gas well 7 | 2021-02-05 | 13:39 | 56.2 | 38.3 | 0.1 | 22 | 14 | 5.4 | 959 | -18.05 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW7 | gas well 7 | 2021-02-11 | 11:17 | 54.4 | 37.8 | 0.3 | 24 | 12 | 7.5 | 975 | -29.57 |  | 30 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW7 | gas well 7 | 2021-02-16 | 11:23 | 54.7 | 37 | 0.4 | 9 | 9 | 7.9 | 960 | -22.65 |  | 30 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW7 | gas well 7 | 2021-02-26 | 12:43 | 54.1 | 35.7 | 0.3 | 16 | 2 | 9.9 | 991 | -25.55 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW7 | gas well 7 | 2021-03-03 | 14:15 | 52.3 | 36.4 | 0.1 | 6 | 24 | 11.2 | 979 | -25.29 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW7 | gas well 7 | 2021-03-09 | 10:09 | 52.1 | 36.6 | 0.1 | 28 | 11 | 11.2 | 973 | -27.89 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW7 | gas well 7 | 2021-03-16 | 13:57 | 52.5 | 36.2 | 0.1 | 35 | 17 | 11.2 | 982 | -25.27 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW7 | gas well 7 | 2021-03-25 | 14:22 | 52.7 | 36.6 | 0.1 | 33 | 16 | 10.6 | 969 | -23.57 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW7 | gas well 7 | 2021-03-30 | 14:14 | 53.3 | 35.9 | 0 | 59 | 14 | 10.8 | 981 | -22.35 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW8 | gas well 8 | 2021-01-04 | 14:53 | 43.7 | 31.7 | 0.2 | 30 | 3 | 24.4 | 972 | -6.54 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW8 | gas well 8 | 2021-01-15 | 9:30 | 65.9 | 32.5 | 0.5 | 36 | 11 | 1.1 | 982 | -6.33 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW8 | gas well 8 | 2021-01-22 | 9:51 | 66.9 | 34.5 | 0.9 | 34 | 21 | 0 | 946 | -9.39 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW8 | gas well 8 | 2021-01-27 | 10:43 | 42 | 31.7 | 0.5 | 21 | 0 | 25.8 | 966 | -7.12 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW8 | gas well 8 | 2021-02-05 | 13:36 | 54.6 | 32.1 | 0.3 | 28 | 5 | 13 | 960 | -5.33 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW8 | gas well 8 | 2021-02-11 | 11:14 | 43 | 30.7 | 0.6 | 29 | 5 | 25.7 | 976 | -8.9 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW8 | gas well 8 | 2021-02-16 | 11:26 | 42.3 | 29.5 | 0.2 | 19 | 0 | 28 | 959 | -5.62 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW8 | gas well 8 | 2021-02-26 | 12:39 | 63.3 | 30.4 | 0.6 | 21 | 0 | 5.7 | 992 | -7.06 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW8 | gas well 8 | 2021-03-03 | 14:07 | 61.1 | 31.8 | 0.5 | 15 | 2 | 6.6 | 979 | -6.27 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW8 | gas well 8 | 2021-03-09 | 10:06 | 51.8 | 31.6 | 0.2 | 35 | 4 | 16.4 | 973 | -7.15 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW8 | gas well 8 | 2021-03-16 | 13:52 | 49.3 | 29.7 | 0 | 40 | 6 | 21 | 982 | -8.07 |  | 20 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW8 | gas well 8 | 2021-03-25 | 14:18 | 51.5 | 30 | 0.1 | 38 | 9 | 18.4 | 970 | -4.62 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW8 | gas well 8 | 2021-03-30 | 14:11 | 52.3 | 28.9 | 0.3 | 48 | 10 | 18.5 | 981 | -5.02 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000GW9 | gas well 9 | 2021-01-04 | 14:55 | 46 | 34.1 | 0.7 | 27 | 4 | 19.2 | 973 | -14.54 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000GW9 | gas well 9 | 2021-01-15 | 9:32 | 50.6 | 33.9 | 0.1 | 32 | 10 | 15.4 | 982 | -13.69 |  | 30 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000GW9 | gas well 9 | 2021-01-22 | 9:53 | 54 | 35.2 | 0.5 | 30 | 15 | 10.3 | 947 | -18.29 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-01-27 | 10:42 | 45.7 | 34.4 | 0.3 | 17 | 6 | 19.6 | 966 | -14.6 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000GW9 | gas well 9 | 2021-02-05 | 13:38 | 46.5 | 33.9 | 0.2 | 24 | 4 | 19.4 | 960 | -12.11 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-02-11 | 11:15 | 42.5 | 32.5 | 0.5 | 27 | 5 | 24.5 | 976 | -17.89 |  | 20 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000GW9 | gas well 9 | 2021-02-16 | 11:24 | 43.2 | 33.6 | 0.1 | 15 | 3 | 23.1 | 960 | -13.99 |  | 20 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-02-26 | 12:41 | 45.2 | 30.3 | 0.2 | 17 | 0 | 24.3 | 992 | -15.32 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-03-03 | 14:17 | 43.1 | 31.5 | 0.2 | 15 | 3 | 25.2 | 979 | -13.57 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000GW9 | gas well 9 | 2021-03-09 | 10:08 | 43.2 | 31.7 | 0.4 | 32 | 4 | 24.7 | 974 | -15.53 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000GW9 | gas well 9 | 2021-03-16 | 13:55 | 41.7 | 30.7 | 0.7 | 34 | 6 | 26.9 | 982 | -15.78 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000GW9 | gas well 9 | 2021-03-25 | 14:20 | 39.9 | 31.1 | 0.3 | 37 | 7 | 28.7 | 970 | -11.71 |  | 20 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-03-25 | 14:20 | 39 | 31.1 | 0.3 | 36 | 8 | 29.6 | 970 | -8.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000GW9 | gas well 9 | 2021-03-30 | 14:12 | 63.1 | 41 | 0.1 | 59 | 8 | 0 | 981 | -7.65 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW1 | leachate well 1 | 2021-01-04 | 14:06 | 64 | 39.7 | 0.6 | 34 | 38 | 0 | 972 | -142.74 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW1 | leachate well 1 | 2021-01-15 | 8:56 | 68.4 | 40.2 | 0.3 | 38 | 53 | 0 | 982 | -116.71 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW1 | leachate well 1 | 2021-01-18 | 15:12 | 69.2 | 40.1 | 0.2 | 41 | 46 | 0 | 970 | -120.25 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW1 | leachate well 1 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW1 | leachate well 1 | 2021-02-01 | 15:06 | 65.8 | 40.2 | 0.3 | 29 | 44 | 0 | 952 | -117.67 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW1 | leachate well 1 | 2021-02-08 | 13:54 | 65.3 | 41 | 0.6 | 29 | 28 | 0 | 956 | -178.23 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW1 | leachate well 1 | 2021-02-15 | 15:32 | 64.9 | 39.8 | 0.3 | 41 | 37 | 0 | 969 | -143.79 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW1 | leachate well 1 | 2021-02-22 | 15:00 | 62.9 | 39 | 0.4 | 39 | 24 | 0 | 969 | -153.04 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW1 | leachate well 1 | 2021-03-02 | 14:56 | 64.8 | 38.9 | 0.5 | 29 | 9 | 0 | 981 | -160.83 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW1 | leachate well 1 | 2021-03-08 | 15:03 | 59.4 | 38.4 | 0.9 | 7 | 13 | 1.3 | 975 | -171.8 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW1 | leachate well 1 | 2021-03-16 | 12:56 | 64.8 | 38 | 1 | 51 | 24 | 0 | 982 | -153.94 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW1 | leachate well 1 | 2021-03-25 | 13:32 | 64.4 | 39.5 | 0.4 | 48 | 23 | 0 | 970 | -148.51 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW1 | leachate well 1 | 2021-03-30 | 13:35 | 64 | 38.4 | 0.6 | 54 | 15 | 0 | 982 | -131.1 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-04 | 14:04 | 42 | 30.4 | 4.9 | 66 | 39 | 22.7 | 972 | -158.38 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-07 | 16:18 | 0.6 | 0.5 | 21.5 | 4 | 1 | 77.4 | 970 | -123.57 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-07 | 16:18 | 0.5 | 0.4 | 21.6 | 3 | 1 | 77.5 | 970 | -37.87 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-08 | 14:32 | 10.8 | 10.5 | 17.5 | 8 | 0 | 61.2 | 972 | -1.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-15 | 8:43 | 18.7 | 14.7 | 14.3 | 47 | 41 | 52.3 | 981 | 0.95 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW2 | leachate well 2 | 2021-01-18 | 15:05 | 9 | 7.5 | 18.4 | 32 | 12 | 65.1 | 972 | -0.21 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-01-25 | 14:50 | 67 | 43.2 | 0.7 | 40 | 107 |  | 965 | -0.1 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-25 | 14:50 | 65.8 | 42.4 | 0.1 | 37 | 99 | 0 | 965 | 38.48 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-27 | 11:10 | 67.7 | 39.1 | 0.1 | 34 | 187 | 0 | 965 | 255.97 |  | 20 |  | Investigation/attention required |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-27 | 11:15 | 66.8 | 39.7 | 0.1 | 31 | 172 | 0 | 965 | -2.88 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-01-29 | 14:58 | 60.9 | 41 | 1.1 | 30 | 51 | 0 | 954 | -111.26 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-02-01 | 14:55 | 61.9 | 41.8 | 0.9 | 46 | 63 | 0 | 952 | -115.76 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-02-01 | 14:56 | 62.2 | 41.6 | 0.8 | 49 | 54 | 0 | 952 | -124.71 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-02-08 | 13:52 | 57.2 | 41.3 | 1.7 | 35 | 28 | 0 | 956 | -190.63 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-02-15 | 0.64583 | 57.3 | 36.9 | 2.2 | 67 | 65 | 3.6 | 969 | -157.01 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-02-22 | 0.61944 | 59.9 | 41 | 1.1 | 71 | 56 | 0 | 969 | -168.85 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-03-02 | 14:43 | 57.6 | 39.5 | 1.7 | 66 | 52 | 1.2 | 980 | -165.31 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW2 | leachate well 2 | 2021-03-08 | 15:01 | 54.4 | 37.9 | 1.3 | 18 | 17 | 6.4 | 975 | -200.8 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW2 | leachate well 2 | 2021-03-16 | 12:54 | 58.2 | 37.8 | 1.7 | 64 | 43 | 2.3 | 982 | -177.42 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW2 | leachate well 2 | 2021-03-25 | 13:26 | 64.6 | 43 | 0.5 | 69 | 71 | 0 | 970 | -174.04 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW2 | leachate well 2 | 2021-03-30 | 13:30 | 62 | 40.1 | 0.7 | 74 | 37 | 0 | 983 | -167.89 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-04 | 13:58 | 28.8 | 21 | 11.8 | 32 | 58 | 38.4 | 971 | -42.64 |  | 25 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-04 | 13:59 | 28.2 | 21.1 | 11.9 | 29 | 60 | 38.8 | 971 | -36.95 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-08 | 14:55 | 67.4 | 43.4 | 0.1 | 49 | 110 |  | 972 | 64.56 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-08 | 14:56 | 66.6 | 43.1 | 0.2 | 51 | 105 | 0 | 972 | -9.06 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-08 | 14:58 | 64.9 | 42 | 0.8 | 59 | 114 | 0 | 970 | -11.87 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-15 | 8:40 | 64.8 | 42.7 | 1 | 54 | 8 | 0 | 980 | -5.87 |  | 30 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW3 | leachate well 3 | 2021-01-18 | 15:02 | 48.8 | 33.1 | 5.7 | 54 | 14 | 12.4 | 969 | -42.78 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-01-18 | 15:02 | 48.3 | 32.8 | 5.8 | 55 | 12 | 13.1 | 969 | -35.99 |  | 25 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-01-25 | 14:38 | 64.9 | 43 | 0.1 | 54 | 114 | 0 | 966 | 201.21 |  | 25 |  | Investigation/attention required |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-25 | 14:40 | 65.1 | 43.2 | 0.1 | 52 | 109 | 0 | 966 | -6.7 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-01-29 | 14:54 | 45 | 32.7 | 5.8 | 21 | 120 | 16.5 | 953 | -58.92 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-01-29 | 14:55 | 42.1 | 30.4 | 6.8 | 25 | 20 | 20.7 | 953 | -50.78 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-01-29 | 14:56 | 42.3 | 30.6 | 6.8 | 23 | 17 | 20.3 | 953 | -27.37 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-02-01 | 14:50 | 64.9 | 43.6 | 0 | 46 | 119 | 0 | 951 | 44.01 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-02-01 | 14:52 | 64.7 | 43.5 | 0.1 | 43 | 111 | 0 | 951 | -5.55 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-02-08 | 13:41 | 65 | 43.7 | 0.2 | 51 | 76 | 0 | 956 | 187.87 |  | 30 |  | Investigation/attention required |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-02-08 | 13:42 | 65.1 | 43.8 | 0 | 54 | 81 | 0 | 956 | 188.18 |  | 100 |  | Investigation/attention required |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-02-08 | 13:43 | 65.2 | 43.7 | 0 | 56 | 84 | 0 | 956 | 188.58 |  | 30 |  | Investigation/attention required |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-02-15 | 0.64028 | 39.6 | 29.3 | 8.1 | 45 | 15 | 23 | 968 | -109.53 |  | 30 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-02-15 | 15:22 | 38.5 | 29.2 | 8.2 | 42 | 16 | 24.1 | 968 | -97.31 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-02-22 | 14:49 | 58.8 | 39.6 | 1.8 | 62 | 13 | 0 | 969 | -64.2 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-03-02 | 14:40 | 57 | 38.8 | 2.1 | 46 | 4 | 2.1 | 982 | -52.19 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW3 | leachate well 3 | 2021-03-08 | 14:49 | 52.7 | 32.3 | 3.1 | 25 | 10 | 11.9 | 976 | -76.59 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW3 | leachate well 3 | 2021-03-16 | 12:48 | 56 | 37.9 | 2.6 | 71 | 13 | 3.5 | 982 | -76.27 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW3 | leachate well 3 | 2021-03-25 | 13:22 | 61.1 | 40.8 | 1.1 | 64 | 14 | 0 | 970 | -42.22 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW3 | leachate well 3 | 2021-03-30 | 13:27 | 59.1 | 39.9 | 1.5 | 75 | 18 | 0 | 981 | -55.24 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW4 | leachate well 4 | 2021-01-04 | 15:28 | 64.2 | 43.8 | 0.8 | 53 | 15 | 0 | 971 | -149.65 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW4 | leachate well 4 | 2021-01-15 | 10:32 | 66.2 | 43.4 | 0.7 | 51 | 7 |  | 981 | -130.8 |  | 100 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW4 | leachate well 4 | 2021-01-18 | 14:56 | 66.1 | 43.2 | 0.9 | 63 | 26 |  | 972 | -120.34 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW4 | leachate well 4 | 2021-01-27 | 11:05 | 62.6 | 43.5 | 0.9 | 52 | 42 | 0 | 966 | -120.7 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW4 | leachate well 4 | 2021-02-01 | 14:43 | 59.6 | 43.3 | 0.6 | 41 | 32 | 0 | 951 | -154.49 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW4 | leachate well 4 | 2021-02-08 | 13:36 | 58.5 | 41.9 | 1.4 | 55 | 9 | 0 | 955 | -165.83 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW4 | leachate well 4 | 2021-02-15 | 0.6375 | 61.3 | 44.6 | 0.9 | 68 | 15 | 0 | 971 | -165.37 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW4 | leachate well 4 | 2021-02-22 | 14:45 | 55.7 | 39.7 | 2 | 61 | 12 | 2.6 | 968 | -167.01 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW4 | leachate well 4 | 2021-03-02 | 14:32 | 51.1 | 36.9 | 3.5 | 69 | 13 | 8.5 | 980 | -194.13 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW4 | leachate well 4 | 2021-03-08 | 14:40 | 53.5 | 38.2 | 3 | 72 | 20 | 5.3 | 977 | -203.89 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW4 | leachate well 4 | 2021-03-16 | 12:44 | 53.3 | 37.5 | 3 | 82 | 16 | 6.2 | 981 | -187.8 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW4 | leachate well 4 | 2021-03-25 | 13:18 | 55.9 | 39.5 | 2.2 | 63 | 30 | 2.4 | 968 | -178.51 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW4 | leachate well 4 | 2021-03-30 | 13:23 | 55.9 | 39.7 | 1.8 | 79 | 29 | 2.6 | 980 | -176.62 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-01-04 | 15:08 | 0.3 | 0.3 | 17.2 | 11 | 16 | 82.2 | 972 | -145.17 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-01-15 | 9:42 | 0.5 | 0.2 | 21.1 | 12 | 11 | 78.2 | 982 | -127.49 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW5 | leachate well 5 | 2021-01-22 | 10:05 | 22.2 | 9.2 | 19.2 | 0 | 0 | 49.4 | 947 | -178.11 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW5 | leachate well 5 | 2021-01-27 | 10:32 | 77.4 | 26.9 | 1.2 | 21 | 27 | 0 | 964 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-02-03 | 12:19 | 14.5 | 5.5 | 17.6 | 0 | 0 | 62.4 | 946 | -117.54 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW5 | leachate well 5 | 2021-02-11 | 11:22 | 0.1 | 0.2 | 23 | 8 | 2 | 76.7 | 974 | -196.15 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-02-16 | 11:14 | 0.1 | 0.2 | 20.9 | 6 | 0 | 78.8 | 959 | -172.39 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW5 | leachate well 5 | 2021-02-26 | 0.53611 | 0 | 0.2 | 19.1 | 0 | 13 | 80.7 | 991 | -151.68 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW5 | leachate well 5 | 2021-03-05 | 13:19 | 77.6 | 26.5 | 0.6 | 11 | 16 | 0 | 984 | 45.04 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-03-05 | 13:20 | 0.2 | 0.2 | 19.9 | 4 | 5 | 79.7 | 984 | -120.3 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-03-05 | 13:20 | 0 | 0.2 | 20.8 | 2 | 2 | 79 | 984 | -103.3 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW5 | leachate well 5 | 2021-03-09 | 10:19 | 0.2 | 0.2 | 20 | 12 | 22 | 79.6 | 973 | -93.02 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW5 | leachate well 5 | 2021-03-16 | 14:06 | 0.2 | 0.2 | 19.2 | 18 | 26 | 80.4 | 981 | -99.86 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW5 | leachate well 5 | 2021-03-25 | 14:33 | 0.2 | 0.2 | 20.3 | 16 | 23 | 79.3 | 970 | -56.59 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW5 | leachate well 5 | 2021-03-30 | 14:22 | 31.3 | 12.1 | 11.9 | 27 | 39 | 44.7 | 981 | -44.22 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW6 | leachate well 6 | 2021-01-04 | 15:09 | 0.3 | 0.2 | 21.6 | 9 | 3 | 77.9 | 971 | -152.64 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW6 | leachate well 6 | 2021-01-15 | 9:44 | 69.2 | 43.6 | 0.7 | 27 | 83 |  | 981 | 3.9 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW6 | leachate well 6 | 2021-01-15 | 9:44 | 68.4 | 43.3 | 0.3 | 32 | 97 |  | 981 | -3.85 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW6 | leachate well 6 | 2021-01-22 | 10:07 | 0 | 0.2 | 19.1 | 0 | 0 | 80.7 | 946 | -178.04 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW6 | leachate well 6 | 2021-01-27 | 10:31 | 0.3 | 0.4 | 14.9 | 25 | 36 | 84.4 | 965 | -139.81 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW6 | leachate well 6 | 2021-02-03 | 12:21 | 0 | 0.1 | 21.3 | 0 | 0 | 78.6 | 948 | -126.95 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW6 | leachate well 6 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW6 | leachate well 6 | 2021-02-16 | 11:12 | 0.2 | 0.3 | 18.2 | 12 | 15 | 81.3 | 958 | -178.01 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW6 | leachate well 6 | 2021-02-26 | 12:53 | 65.9 | 37.4 | 0.8 | 7 | 22 | 0 | 990 | 0.14 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW6 | leachate well 6 | 2021-03-05 | 13:18 | 0.2 | 0.2 | 20.6 | 12 | 7 | 79 | 984 | -120.11 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW6 | leachate well 6 | 2021-03-09 | 10:20 | 0.1 | 0.1 | 21.1 | 9 | 2 | 78.7 | 973 | -122.3 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW6 | leachate well 6 | 2021-03-16 | 14:08 | 0.1 | 0.1 | 21 | 13 | 6 | 78.8 | 982 | -39.08 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW6 | leachate well 6 | 2021-03-25 | 14:34 | 24.9 | 15.4 | 12.9 | 17 | 5 | 46.8 | 969 | -0.85 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW6 | leachate well 6 | 2021-03-30 | 14:23 | 0.1 | 0.1 | 20 | 20 | 10 | 79.8 | 980 | -27.96 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-01-04 | 14:10 | 31.1 | 4.5 | 13.5 | 21 | 30 | 50.9 | 973 | -6.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-01-08 | 14:29 | 71.3 | 18.3 | 1.9 | 14 | 0 | 8.5 | 972 | -2.85 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-01-15 | 9:00 | 65.9 | 27.3 | 1.1 | 31 | 9 | 5.7 | 982 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW7 | Leachate well 7 | 2021-01-15 | 9:01 | 67.8 | 31.6 | 1.1 | 33 | 6 | 0 | 982 | -0.23 |  | 20 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW7 | Leachate well 7 | 2021-01-18 | 15:15 | 74.2 | 36.5 | 0.6 | 38 | 67 |  | 970 | -0.07 |  | 20 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-01-25 | 0.62222 | 71.4 | 34.1 | 0.7 | 33 | 67 | 0 | 966 | -0.1 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-02-05 | [13 empty] | 8 | Unable to find sample point | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-02-11 | [13 empty] | 8 | Unable to find sample point | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-02-16 | [13 empty] | 8 | Unable to find sample point | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-02-22 | 14:47 | 62.4 | 42.3 | 0.4 | 70 | 29 | 0 | 968 | -154.68 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-02-26 | 14:55 | 23.6 | 13.6 | 8.6 | 3 | 4 | 54.2 | 990 | 0.59 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-03-02 | 15:00 | 70.1 | 30.7 | 0.2 | 26 | 32 | 0 | 981 | 0.35 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-03-02 | 15:02 | 49.8 | 23 | 5.3 | 20 | 27 | 21.9 | 981 | -25.44 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-03-02 | 15:04 | 48.7 | 22.8 | 5.6 | 12 | 17 | 22.9 | 981 | 1.2 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW7 | Leachate well 7 | 2021-03-08 | 15:06 | 65.3 | 32.5 | 0.3 | 8 | 6 | 1.9 | 971 | 1.32 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW7 | Leachate well 7 | 2021-03-08 | 15:08 | 66.6 | 32.4 | 0.7 | 9 | 6 | 0.3 | 971 | -0.21 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW7 | Leachate well 7 | 2021-03-16 | 12:59 | 23.5 | 12.4 | 13.7 | 29 | 15 | 50.4 | 983 | -5.94 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW7 | Leachate well 7 | 2021-03-16 | 13:00 | 22.6 | 12.1 | 13.7 | 25 | 9 | 51.6 | 983 | -0.69 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW7 | Leachate well 7 | 2021-03-25 | 13:35 | 63.7 | 30.4 | 0.8 | 37 | 22 | 5.1 | 970 | -0.52 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-03-25 | 13:37 | 55.4 | 26.3 | 2.9 | 32 | 7 | 15.4 | 970 | -9.16 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-03-25 | 13:37 | 53.4 | 26 | 3.3 | 30 | 7 | 17.3 | 970 | -103.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW7 | Leachate well 7 | 2021-03-30 | 13:38 | 4.7 | 3.3 | 17.7 | 35 | 17 | 74.3 | 981 | 0.16 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-01-08 | 14:47 | 55.8 | 37 | 1.7 | 46 | 60 | 5.5 | 970 | -55.34 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000LW8 | leachate well 8 | 2021-01-18 | 14:59 | 58.8 | 36.4 | 2.6 | 63 | 22 | 2.2 | 970 | -121.4 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-02-01 | 14:46 | 57.8 | 37.1 | 4.8 | 30 | 6 | 0.3 | 952 | -120.95 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-02-01 | 0.61597 | 57.6 | 39.5 | 2.6 | 31 | 4 | 0.3 | 952 | -112.53 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-02-08 | 13:38 | 63.7 | 43.3 | 0.3 | 53 | 56 | 0 | 956 | -155.67 |  | 30 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-02-08 | 13:39 | 64 | 43.5 | 0.2 | 54 | 72 | 0 | 956 | -173.67 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-02-15 | 15:20 | 59.5 | 39.9 | 1.9 | 57 | 13 | 0 | 969 | -161.19 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-02-26 | [13 empty] | 6 | No safe access | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-03-02 | 14:35 | 62.2 | 41.8 | 0.4 | 60 | 16 | 0 | 980 | -185.99 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000LW8 | leachate well 8 | 2021-03-08 | 14:42 | 62.6 | 42.1 | 0.8 | 56 | 20 | 0 | 977 | -199.13 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR000LW8 | leachate well 8 | 2021-03-16 | 12:46 | 63.7 | 41.9 | 0.8 | 58 | 32 | 0 | 984 | -179.69 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR000LW8 | leachate well 8 | 2021-03-25 | 13:21 | 63.5 | 42.1 | 0.4 | 61 | 25 | 0 | 970 | -170.65 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000LW8 | leachate well 8 | 2021-03-30 | 13:25 | 62.3 | 40.5 | 0.3 | 76 | 22 | 0 | 980 | -167.61 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR000SR1 | side riser 1 | 2021-01-04 | 13:36 | 49.3 | 34.7 | 0.3 | 13 | 11 | 15.7 | 972 | -100.07 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000SR1 | side riser 1 | 2021-01-04 | 13:37 | 49.1 | 34.7 | 0.2 | 13 | 18 | 16 | 972 | -118.71 |  | 50 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000SR1 | side riser 1 | 2021-01-08 | 15:11 | 48.8 | 34.7 | 0.5 | 19 | 23 | 16 | 969 | -85.99 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000SR1 | side riser 1 | 2021-02-15 | 13:52 | 38.5 | 31 | 0.3 | 9 | 7 | 30.2 | 969 | -117.28 |  | 50 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000SR1 | side riser 1 | 2021-02-15 | 13:53 | 39.2 | 31.2 | 0.2 | 9 | 8 | 29.4 | 969 | -91.89 |  | 20 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000UNI | Uniflare | 2021-01-04 | 10:21 | 41.7 | 29.8 | 3.7 | 45 | 13 | 24.8 | 971 | -174.63 | 1701 | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000UNI | Uniflare | 2021-01-07 | 14:08 | 45.6 | 31.4 | 3 | 38 | 131 | 20 | 967 | -151.58 | 1702 | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000UNI | Uniflare | 2021-01-11 | 10:35 | 46.6 | 32.6 | 2.3 | 41 | 49 | 18.5 | 968 | -107.41 | 1704 | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR000UNI | Uniflare | 2021-01-15 | [13 empty] | 23 | Sample point frozen | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR000UNI | Uniflare | 2021-01-15 | 14:40 | 48.8 | 33.1 | 1.8 | 41 | 100 | 16.3 | 978 | -133.49 | 1701 | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000UNI | Uniflare | 2021-01-18 | 9:29 | 50.1 | 33.5 | 1.5 | 44 | 55 | 14.9 | 972 | -135.91 | 1700 | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR000UNI | Uniflare | 2021-01-22 | 14:12 | 47.4 | 34 | 1.8 | 32 | 161 | 16.8 | 942 | -178.39 | 1700 | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000UNI | Uniflare | 2021-01-25 | 9:28 | 44.6 | 33.9 | 1.4 | 33 | 0 | 20.1 | 961 | -226.93 | 1702 | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR000UNI | Uniflare | 2021-01-29 | 9:54 | 46.7 | 33.4 | 2 | 30 | 161 | 17.9 | 948 | -159.79 | 1701 | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-01 | 9:27 | 45.1 | 34 | 1.6 | 37 | 0 | 19.3 | 946 | -197.98 | 1701 | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-05 | 10:19 | 47.4 | 33.1 | 2 | 28 | 144 | 17.5 | 956 | -148.02 | 1705 | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-11 | 9:19 | 41.4 | 32.1 | 2.1 | 31 | 4 | 24.4 | 971 | -195.9 | 1702 | 100 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR000UNI | Uniflare | 2021-02-15 | 11:21 | 45.9 | 33.2 | 1.4 | 43 | 107 | 19.5 | 969 | -178.46 | 1705 | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-18 | 14:57 | 47.8 | 34.5 | 1.8 | 18 | 123 | 15.9 | 950 | -156.33 | 1702 | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-22 | 11:07 | 46.7 | 32.8 | 2.1 | 26 | 28 | 18.4 | 965 | -144.17 | 1700 | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-02-26 | 11:39 | 43.3 | 30.6 | 2.8 | 18 | 0 | 23.3 | 987 | -176.59 | 1704 | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-03-02 | 0.41528 | 42.9 | 33.4 | 1.4 | 4 | 0 | 22.3 | 978 | -200.26 | 1702 | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000UNI | Uniflare | 2021-03-05 | 0.42847 | 43.3 | 33.2 | 1.5 | 10 | 0 | 22 | 980 | -192.66 | 1702 | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR000UNI | Uniflare | 2021-03-08 | 0.44167 | 44.1 | 33.7 | 1.4 | 16 | 0 | 20.8 | 973 | -206.85 | 1700 | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR000UNI | Uniflare | 2021-03-15 | 0.47083 | 41.6 | 29.4 | 3.1 | 30 | 30 | 25.9 | 972 | -178.6 | 1700 | 100 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR000UNI | Uniflare | 2021-03-19 | 0.39306 | 41.6 | 30.3 | 3.4 | 23 | 2 | 24.7 | 978 | -150.29 | 1405 | 100 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-03-19 | 0.63681 | 42.6 | 30.2 | 4.5 | 35 | 92 | 22.7 | 985 | -213.71 | 1703 | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-03-22 | 0.59028 | 43.5 | 31 | 3.4 | 28 | 13 | 22.1 | 974 | -218.24 | 1702 | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-03-26 | 0.39792 | 51 | 33.8 | 2 | 37 | 47 | 13.2 | 956 | -192.97 | 1603 | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR000UNI | Uniflare | 2021-03-29 | 0.59514 | 46.3 | 32.1 | 3 | 33 | 47 | 18.6 | 976 | -189.52 | 1600 | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW10 | gas well 10 | 2021-01-04 | 0.61875 | 46.5 | 34.6 | 0.5 | 33 | 10 | 18.4 | 972 | -8.4 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW10 | gas well 10 | 2021-01-15 | 9:29 | 66.5 | 37 | 0.3 | 41 | 16 | 0 | 982 | -7.79 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW10 | gas well 10 | 2021-01-22 | 9:50 | 65.7 | 39.8 | 0.6 | 38 | 30 | 0 | 946 | -10.34 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-01-27 | 10:48 | 44.2 | 34.3 | 0.3 | 18 | 0 | 21.2 | 966 | -7.69 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW10 | gas well 10 | 2021-02-05 | 13:35 | 60.1 | 37.3 | 0.3 | 38 | 12 | 2.3 | 959 | -6.33 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-02-11 | 0.46736 | 44.1 | 34.3 | 0.5 | 31 | 7 | 21.1 | 975 | -9.96 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW10 | gas well 10 | 2021-02-16 | 0.47778 | 51.2 | 33.1 | 0.1 | 19 | 0 | 15.6 | 960 | -5.54 |  | 30 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-02-26 | 0.52569 | 64.1 | 35.8 | 0.4 | 28 | 0 | 0 | 991 | -7.2 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-03-03 | 0.58681 | 64.5 | 36.7 | 0.2 | 15 | 0 | 0 | 977 | -6.65 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW10 | gas well 10 | 2021-03-09 | 0.42014 | 59.8 | 36.2 | 0.2 | 41 | 11 | 3.8 | 973 | -7.74 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW10 | gas well 10 | 2021-03-16 | 0.57639 | 58.4 | 35.6 | 0.1 | 50 | 14 | 5.9 | 982 | -8.5 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW10 | gas well 10 | 2021-03-25 | 0.59444 | 64.3 | 36.4 | 0.1 | 47 | 15 | 0 | 970 | -5.55 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-03-25 | 0.59514 | 61.6 | 35.3 | 0 | 42 | 10 | 3.1 | 970 | -5.88 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW10 | gas well 10 | 2021-03-30 | 0.58958 | 54.9 | 33.9 | 0.2 | 54 | 12 | 11 | 981 | -6.84 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW11 | gas well 11 | 2021-01-04 | 0.61806 | 44.1 | 36.1 | 0.6 | 32 | 12 | 19.2 | 972 | -14.34 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW11 | gas well 11 | 2021-01-15 | 0.39375 | 49.7 | 37.4 | 0.1 | 43 | 24 | 12.8 | 982 | -12.56 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW11 | gas well 11 | 2021-01-22 | 9:49 | 53.5 | 37.6 | 0.2 | 39 | 49 | 8.7 | 946 | -18.5 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW11 | gas well 11 | 2021-01-27 | 10:51 | 46.9 | 37.3 | 0.1 | 35 | 26 | 15.7 | 965 | -14.18 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW11 | gas well 11 | 2021-02-05 | 0.56458 | 49.2 | 38 | 0.2 | 37 | 18 | 12.6 | 959 | -12.03 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW11 | gas well 11 | 2021-02-11 | 11:09 | 42.6 | 36.2 | 0.6 | 41 | 12 | 20.6 | 974 | -18.07 |  | 30 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW11 | gas well 11 | 2021-02-16 | 11:31 | 44.1 | 36.4 | 0.1 | 29 | 16 | 19.4 | 960 | -13.83 |  | 20 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW11 | gas well 11 | 2021-02-26 | 12:36 | 49.3 | 34.1 | 0.3 | 23 | 0 | 16.3 | 990 | -15.6 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW11 | gas well 11 | 2021-03-03 | 14:19 | 46.6 | 35.7 | 0 | 32 | 17 | 17.7 | 978 | -13.62 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW11 | gas well 11 | 2021-03-09 | 10:03 | 45.8 | 35.8 | 0.1 | 44 | 13 | 18.3 | 973 | -15.76 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW11 | gas well 11 | 2021-03-16 | 0.575 | 45.6 | 35.4 | 0.1 | 55 | 24 | 18.9 | 982 | -16.35 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW11 | gas well 11 | 2021-03-25 | 14:14 | 48.1 | 37.2 | 0.2 | 48 | 23 | 14.5 | 970 | -10.9 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW11 | gas well 11 | 2021-03-30 | 14:07 | 47.7 | 34.8 | 0.1 | 67 | 24 | 17.4 | 981 | -11.59 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW12 | gas well 12 | 2021-01-04 | 14:48 | 43.3 | 35 | 0.9 | 24 | 10 | 20.8 | 971 | -37.71 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW12 | gas well 12 | 2021-01-15 | 9:26 | 57.2 | 36.6 | 0.2 | 30 | 17 | 6 | 981 | -35.92 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW12 | gas well 12 | 2021-01-22 | 9:47 | 57.6 | 38.6 | 0.5 | 37 | 226 | 3.3 | 944 | -47.41 |  | 30 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW12 | gas well 12 | 2021-01-27 | 10:50 | 44 | 35.1 | 0.5 | 16 | 1 | 20.4 | 966 | -36.6 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW12 | gas well 12 | 2021-02-05 | 13:32 | 47.4 | 35.8 | 0.9 | 13 | 4 | 15.9 | 960 | -34.9 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW12 | gas well 12 | 2021-02-11 | 11:11 | 42.2 | 35.4 | 0.5 | 31 | 10 | 21.9 | 975 | -47.88 |  | 40 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW12 | gas well 12 | 2021-02-16 | 11:30 | 43.7 | 34.4 | 0.2 | 14 | 0 | 21.7 | 960 | -40.11 |  | 30 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW12 | gas well 12 | 2021-02-26 | 12:34 | 50.1 | 33.5 | 0.7 | 1 | 0 | 15.7 | 990 | -40.99 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW12 | gas well 12 | 2021-03-03 | 14:20 | 47.8 | 34.8 | 0.1 | 22 | 5 | 17.3 | 978 | -42.19 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW12 | gas well 12 | 2021-03-09 | 10:01 | 47.6 | 34.6 | 0.4 | 31 | 6 | 17.4 | 972 | -46.18 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW12 | gas well 12 | 2021-03-16 | 13:47 | 47.9 | 34.3 | 0.5 | 36 | 12 | 17.3 | 983 | -44.91 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW12 | gas well 12 | 2021-03-25 | 14:13 | 49.6 | 35.3 | 0.3 | 37 | 19 | 14.8 | 968 | -42.26 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW12 | gas well 12 | 2021-03-30 | 14:06 | 46.3 | 33.6 | 0.4 | 37 | 11 | 19.7 | 982 | -41.44 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW13 | gas well 13 | 2021-01-15 | 0.41389 | 52.5 | 33.1 | 1.2 | 26 | 18 | 13.2 | 980 | -143.73 |  | 20 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW13 | gas well 13 | 2021-01-22 | 10:18 | 47.3 | 31.4 | 3.6 | 16 | 24 | 17.7 | 945 | -0.36 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW13 | gas well 13 | 2021-01-27 | 10:55 | 48.7 | 34.1 | 1.4 | 17 | 28 | 15.8 | 964 | -0.12 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW13 | gas well 13 | 2021-02-03 | 12:35 | 53.1 | 36.7 | 0.2 | 21 | 35 | 10 | 948 | -16.87 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW13 | gas well 13 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW13 | gas well 13 | 2021-02-16 | 11:36 | 47.2 | 35.1 | 0.2 | 14 | 28 | 17.5 | 959 | -19.73 |  | 20 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW13 | gas well 13 | 2021-02-26 | 13:06 | 47.7 | 33.6 | 0.2 | 17 | 20 | 18.5 | 989 | -19.94 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW13 | gas well 13 | 2021-03-05 | 13:26 | 37.2 | 27.8 | 4.2 | 8 | 11 | 30.8 | 983 | -22.08 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW13 | gas well 13 | 2021-03-09 | 10:32 | 45 | 32.3 | 1.1 | 27 | 19 | 21.6 | 972 | -21.52 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW13 | gas well 13 | 2021-03-16 | 14:19 | 53.4 | 34.1 | 0 | 35 | 32 | 12.5 | 981 | -20.86 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW13 | gas well 13 | 2021-03-25 | 14:46 | 57.5 | 36.1 | 0.1 | 42 | 30 | 6.3 | 968 | -18.97 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW13 | gas well 13 | 2021-03-30 | 14:37 | 54.6 | 35 | 0.1 | 47 | 25 | 10.3 | 979 | -18.01 |  | 20 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-01-04 | 15:17 | 61.3 | 41.6 | 0.7 | 24 | 25 | 0 | 971 | -20.24 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-01-04 | 15:18 | 59.4 | 39.7 | 0 | 26 | 33 | 0.9 | 971 | -57.76 |  | 40 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-01-15 | 0.41181 | 46.7 | 34.9 | 0.7 | 27 | 21 | 17.7 | 981 | -76.71 |  | 40 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW14 | gas well 14 | 2021-01-22 | 10:16 | 45 | 35.1 | 0.7 | 18 | 14 | 19.2 | 945 | -97.36 |  | 40 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-01-27 | 10:54 | 41 | 34.2 | 0.8 | 16 | 14 | 24 | 964 | -75.01 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-02-03 | 12:32 | 43 | 35 | 0.3 | 23 | 31 | 21.7 | 948 | -73.34 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-02-11 | 0.46181 | 39.5 | 33.6 | 0.6 | 40 | 20 | 26.3 | 973 | -100.66 |  | 40 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-02-16 | 11:34 | 39.8 | 34.1 | 0.5 | 13 | 13 | 25.6 | 952 | -86.72 |  | 30 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-02-26 | 13:05 | 43.2 | 31.6 | 0.4 | 16 | 13 | 24.8 | 990 | -90.58 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-03-05 | 13:25 | 39.4 | 32.7 | 0.5 | 6 | 7 | 27.4 | 983 | -102.22 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW14 | gas well 14 | 2021-03-09 | 10:30 | 40.5 | 32.9 | 0.7 | 25 | 10 | 25.9 | 972 | -101.58 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW14 | gas well 14 | 2021-03-16 | 14:16 | 39.7 | 32.2 | 0.7 | 30 | 12 | 27.4 | 981 | -92.1 |  | 40 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW14 | gas well 14 | 2021-03-16 | 14:17 | 40 | 32.3 | 0.2 | 34 | 12 | 27.5 | 981 | -47.19 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW14 | gas well 14 | 2021-03-25 | 14:44 | 64.4 | 43 | 0 | 38 | 39 | 0 | 968 | -34.36 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-03-25 | 14:44 | 63.4 | 42.9 | 0.3 | 31 | 27 | 0 | 968 | 11 |  | 20 |  | Investigation/attention required |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW14 | gas well 14 | 2021-03-30 | 14:36 | 45.9 | 34.3 | 0.2 | 40 | 16 | 19.6 | 979 | -57.58 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW15 | gas well 15 | 2021-01-04 | 15:15 | 4.6 | 16.8 | 4.8 | 25 | 15 | 73.8 | 971 | -18.07 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW15 | gas well 15 | 2021-01-15 | 9:52 | 0.7 | 0.3 | 12.7 | 29 | 32 | 86.3 | 981 | -0.47 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW15 | gas well 15 | 2021-01-22 | 10:15 | 0.2 | 0.3 | 18 | 17 | 15 | 81.5 | 945 | -0.35 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW15 | gas well 15 | 2021-01-27 | 10:53 | 5.5 | 14.9 | 6.5 | 24 | 10 | 73.1 | 965 | -21.21 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW15 | gas well 15 | 2021-02-03 | 12:30 | 7.6 | 15.7 | 6.1 | 28 | 23 | 70.6 | 948 | -19.7 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW15 | gas well 15 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW15 | gas well 15 | 2021-02-16 | 11:33 | 7.4 | 15.1 | 5.8 | 22 | 9 | 71.7 | 960 | -18.83 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW15 | gas well 15 | 2021-02-26 | 13:03 | 6.4 | 13.4 | 7.2 | 20 | 20 | 73 | 989 | -18.92 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW15 | gas well 15 | 2021-03-05 | 13:23 | 3.6 | 12.9 | 8.1 | 6 | 6 | 75.4 | 983 | -18.47 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW15 | gas well 15 | 2021-03-09 | 10:29 | 5.5 | 13.4 | 7.8 | 25 | 7 | 73.3 | 974 | -17.86 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW15 | gas well 15 | 2021-03-16 | 14:15 | 6.4 | 12.7 | 10.7 | 31 | 12 | 70.2 | 982 | -17.37 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW15 | gas well 15 | 2021-03-25 | 14:42 | 12.9 | 16.9 | 2.3 | 36 | 17 | 67.9 | 968 | -9.82 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW15 | gas well 15 | 2021-03-30 | 0.60694 | 7.3 | 13.6 | 6.8 | 37 | 15 | 72.3 | 981 | -14.35 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW16 | gas well 16 | 2021-01-04 | 15:14 | 50.7 | 36.9 | 0.8 | 36 | 61 | 11.6 | 971 | -98.85 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW16 | gas well 16 | 2021-01-15 | 9:50 | 56.3 | 38 | 0.6 | 37 | 43 | 5.1 | 983 | -91.51 |  | 35 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW16 | gas well 16 | 2021-01-22 | 10:14 | 53.8 | 39.5 | 0.8 | 27 | 96 | 5.9 | 945 | -123.17 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW16 | gas well 16 | 2021-01-27 | 0.43611 | 50.5 | 36.9 | 0.8 | 32 | 27 | 11.8 | 965 | -90.38 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW16 | gas well 16 | 2021-02-03 | 12:29 | 53.1 | 38.7 | 0.3 | 46 | 87 | 7.9 | 948 | -86.57 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW16 | gas well 16 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW16 | gas well 16 | 2021-02-16 | 11:11 | 49.4 | 37.2 | 0.7 | 22 | 37 | 12.7 | 959 | -119.85 |  | 35 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW16 | gas well 16 | 2021-02-26 | 13:02 | 51.7 | 35.2 | 0.4 | 30 | 87 | 12.7 | 990 | -107.39 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW16 | gas well 16 | 2021-03-05 | 13:22 | 48.7 | 36 | 0.6 | 13 | 18 | 14.7 | 984 | -122.61 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW16 | gas well 16 | 2021-03-09 | 10:27 | 50.3 | 36.6 | 0.4 | 44 | 55 | 12.7 | 972 | -128.79 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW16 | gas well 16 | 2021-03-16 | 14:14 | 50.5 | 36.2 | 0.2 | 50 | 57 | 13.1 | 981 | -118 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW16 | gas well 16 | 2021-03-25 | 14:41 | 51.9 | 36.8 | 0.1 | 45 | 59 | 11.2 | 968 | -113.78 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW16 | gas well 16 | 2021-03-30 | 14:33 | 50.8 | 35.6 | 0.1 | 64 | 68 | 13.5 | 979 | -109.46 |  | 35 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW17 | gas well 17 | 2021-01-15 | 9:46 | 53.6 | 37.8 | 0.2 | 40 | 78 | 8.4 | 981 | -0.52 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW17 | gas well 17 | 2021-01-22 | 10:09 | 45.2 | 37.1 | 0.9 | 14 | 51 | 16.8 | 945 | -2.38 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW17 | gas well 17 | 2021-01-27 | 10:29 | 46.8 | 36.7 | 0.4 | 34 | 65 | 16.1 | 964 | -2.59 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW17 | gas well 17 | 2021-02-03 | 12:23 | 45.6 | 36.1 | 0.4 | 16 | 53 | 17.9 | 945 | -2.88 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW17 | gas well 17 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW17 | gas well 17 | 2021-02-16 | 11:08 | 45.2 | 35.6 | 0.4 | 36 | 40 | 18.8 | 958 | -1.51 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW17 | gas well 17 | 2021-02-26 | 12:55 | 48.2 | 34.6 | 0.3 | 20 | 37 | 16.9 | 990 | -1.72 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW17 | gas well 17 | 2021-03-05 | 13:16 | 41.7 | 33.9 | 0.5 | 25 | 28 | 23.9 | 984 | -2.88 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW17 | gas well 17 | 2021-03-09 | 10:22 | 46 | 34.6 | 0.8 | 25 | 24 | 18.6 | 972 | -2.76 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW17 | gas well 17 | 2021-03-16 | 14:09 | 44.2 | 34.1 | 0.4 | 34 | 30 | 21.3 | 981 | -2.55 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW17 | gas well 17 | 2021-03-25 | 14:36 | 49.4 | 35.6 | 0.2 | 40 | 54 | 14.8 | 969 | -1.75 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW17 | gas well 17 | 2021-03-30 | 14:25 | 47.6 | 35 | 0.3 | 49 | 28 | 17.1 | 980 | -1.53 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-01-04 | 15:13 | 48.2 | 37.3 | 2.5 | 56 | 87 | 12 | 971 | -1.48 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-01-15 | 0.40903 | 63.2 | 42.3 | 1.3 | 55 | 197 | 0 | 981 | -0.5 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW18 | gas well 18 | 2021-01-22 | 10:12 | 48.8 | 39.4 | 0.8 | 28 | 224 | 11 | 945 | -0.59 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW18 | gas well 18 | 2021-01-27 | 10:25 | 41.9 | 35 | 3.6 | 11 | 37 | 19.5 | 965 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-02-03 | 12:28 | 58.7 | 43 | 0.2 | 61 | 205 | 0 | 947 | -0.45 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW18 | gas well 18 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-02-16 | 10:47 | 54.6 | 40.5 | 0.9 | 23 | 173 | 4 | 958 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW18 | gas well 18 | 2021-02-26 | 13:01 | 54.3 | 37.3 | 0.9 | 39 | 160 | 7.5 | 990 | -0.02 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW18 | gas well 18 | 2021-03-05 | 13:12 | 39.9 | 33.7 | 2.6 | 11 | 45 | 23.8 | 983 | -2.62 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-03-09 | 10:26 | 51.2 | 37.7 | 2.5 | 56 | 122 | 8.6 | 972 | -0.68 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW18 | gas well 18 | 2021-03-16 | 14:13 | 56.8 | 39.3 | 1.1 | 54 | 117 | 2.8 | 981 | -0.5 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW18 | gas well 18 | 2021-03-25 | 14:39 | 60.2 | 41.6 | 1.2 | 43 | 154 | 0 | 970 | -0.73 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW18 | gas well 18 | 2021-03-30 | 14:31 | 59.4 | 41 | 0.5 | 54 | 156 | 0 | 981 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW18 | gas well 18 | 2021-03-30 | 14:32 | 60.6 | 43.2 | 0.4 | 59 | 206 | 0 | 981 | -0.31 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-01-04 | 15:23 | 41.9 | 34.8 | 0.4 | 23 | 32 | 22.9 | 971 | -8.83 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-01-15 | 10:15 | 50.5 | 37.2 | 0.5 | 19 | 30 | 11.8 | 981 | -8.35 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW19 | gas well 19 | 2021-01-22 | 10:35 | 44.4 | 36.8 | 0.4 | 10 | 35 | 18.4 | 944 | -4.32 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW19 | gas well 19 | 2021-01-27 | 10:20 | 44.2 | 35 | 0.2 | 22 | 15 | 20.6 | 965 | -14.14 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-02-03 | 12:53 | 55.9 | 40.4 | 0 | 11 | 45 | 3.7 | 947 | -3.51 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW19 | gas well 19 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-02-16 | 10:45 | 58.3 | 40.8 | 0.1 | 30 | 68 | 0.8 | 959 | -0.36 |  | 20 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW19 | gas well 19 | 2021-02-26 | 13:20 | 60.3 | 40.7 | 0.2 | 11 | 56 | 0 | 989 | -52.2 |  | 25 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW19 | gas well 19 | 2021-03-05 | 13:10 | 30.9 | 29.1 | 1.2 | 21 | 15 | 38.8 | 984 | -93.21 |  | 25 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-03-05 | 13:11 | 25.8 | 26.8 | 1.1 | 16 | 2 | 46.3 | 984 | -40.26 |  | 20 |  | Investigation/attention required |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-03-05 | 13:11 | 24.8 | 26.2 | 1.1 | 14 | 1 | 47.9 | 984 | -24.92 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW19 | gas well 19 | 2021-03-09 | 11:27 | 65.8 | 40.7 | 0.3 | 19 | 70 | 0 | 972 | 3.38 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW19 | gas well 19 | 2021-03-09 | 11:29 | 65.7 | 41.7 | 0 | 25 | 58 | 0 | 972 | -0.35 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW19 | gas well 19 | 2021-03-16 | 14:30 | 64.4 | 41.4 | 0.1 | 28 | 66 | 0 | 981 | -10.92 |  | 25 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW19 | gas well 19 | 2021-03-16 | 14:30 | 63.9 | 41.4 | 0.7 | 23 | 47 | 0 | 981 | -0.09 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW19 | gas well 19 | 2021-03-25 | 14:59 | 59.8 | 38.7 | 0.1 | 29 | 62 | 1.4 | 968 | -9.44 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW19 | gas well 19 | 2021-03-30 | 14:51 | 51.6 | 36.1 | 0.1 | 35 | 22 | 12.2 | 979 | -5.68 |  | 20 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-01-04 | 15:21 | 57.1 | 39.3 | 0.1 | 24 | 77 | 3.5 | 971 | -21.85 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-01-15 | 10:13 | 50.4 | 36.5 | 0.6 | 19 | 49 | 12.5 | 980 | -90.14 |  | 20 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW20 | gas well 20 | 2021-01-22 | 10:32 | 42.6 | 35.1 | 0.3 | 12 | 76 | 22 | 944 | -112.13 |  | 20 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW20 | gas well 20 | 2021-01-27 | [12 empty] | SITE WORKING CLOSE BY | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-02-05 | [12 empty] | Site working in area | 6 | No safe access | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW20 | gas well 20 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-02-16 | 11:49 | 47.3 | 35.5 | 0.5 | 9 | 79 | 16.7 | 957 | -69.18 |  | 20 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW20 | gas well 20 | 2021-02-26 | 13:18 | 44.4 | 33.9 | 0.1 | 8 | 60 | 21.6 | 988 | -76.19 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW20 | gas well 20 | 2021-03-05 | 13:43 | 36.8 | 33 | 0.1 | 4 | 49 | 30.1 | 982 | -104.22 |  | 50 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-03-05 | 13:43 | 36.1 | 33.1 | 0.1 | 3 | 46 | 30.7 | 982 | -0.56 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW20 | gas well 20 | 2021-03-09 | 11:26 | 63.9 | 41.5 | 0.4 | 18 | 74 | 0 | 971 | 31.38 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW20 | gas well 20 | 2021-03-16 | 14:28 | 5.6 | 3.2 | 16.6 | 25 | 36 | 74.6 | 980 | -2.36 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW20 | gas well 20 | 2021-03-25 | 14:58 | 64.3 | 39.9 | 0.2 | 27 | 116 | 0 | 967 | 21.92 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW20 | gas well 20 | 2021-03-30 | 14:49 | 30.6 | 20.6 | 9 | 30 | 46 | 39.8 | 978 | 5.07 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW21 | gas well 21 | 2021-01-04 | 15:19 | 70.6 | 36.4 | 0.8 | 32 | 23 | 0 | 971 | -152.46 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW21 | gas well 21 | 2021-01-15 | 10:11 | 74 | 35.6 | 0.9 | 28 | 27 |  | 982 | -147.52 |  | 100 |  | Condition good |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW21 | gas well 21 | 2021-01-22 | 10:31 | 71.3 | 35.4 | 0 | 24 | 186 | 0 | 944 | -179.21 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW21 | gas well 21 | 2021-01-27 | 10:58 | 68.7 | 35.8 | 0.9 | 22 | 36 | 0 | 964 | -135.42 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW21 | gas well 21 | 2021-02-03 | 12:48 | 70.9 | 34.9 | 0.5 | 20 | 48 | 0 | 947 | -136.15 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW21 | gas well 21 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW21 | gas well 21 | 2021-02-16 | 11:47 | 69.6 | 34.1 | 0.8 | 21 | 51 | 0 | 952 | -167.15 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW21 | gas well 21 | 2021-02-26 | 13:16 | 67.5 | 32.7 | 0.8 | 16 | 42 | 0 | 988 | -170.08 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW21 | gas well 21 | 2021-03-05 | 0.56944 | 66.1 | 33.2 | 0.8 | 17 | 29 | 0 | 982 | -202.88 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW21 | gas well 21 | 2021-03-09 | 0.47431 | 65.4 | 32.6 | 0.9 | 28 | 19 | 1.1 | 971 | -205.97 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW21 | gas well 21 | 2021-03-16 | 0.60208 | 67.9 | 32.2 | 0.8 | 35 | 51 | 0 | 980 | -191.77 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW21 | gas well 21 | 2021-03-25 | 0.62222 | 70 | 32.6 | 0.7 | 36 | 22 | 0 | 967 | -184.08 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW21 | gas well 21 | 2021-03-30 | 0.61597 | 66.5 | 30.9 | 0.7 | 43 | 36 | 1.9 | 978 | -176.78 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW22 | gas well 22 | 2021-02-03 | 0.53472 | 51.2 | 37.9 | 0.1 | 9 | 91 | 10.8 | 947 | -39.1 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-01-15 | [13 empty] | 10 | GTE Line flooded | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW23 | gas well 23 | 2021-01-22 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-01-27 | [13 empty] | 10 | GTE Line flooded | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW23 | gas well 23 | 2021-02-05 | [13 empty] | 10 | GTE Line flooded | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW23 | gas well 23 | 2021-02-16 | [13 empty] | 10 | GTE Line flooded | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-02-26 | 0.55972 | 36.7 | 21.8 | 7.2 | 14 | 683 | 34.3 | 989 | -0.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-02-26 | 13:27 | 46.3 | 27.3 | 3.8 | 13 | 931 | 22.6 | 989 | -0.03 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-02-26 | 13:28 | 49.8 | 28.5 | 2.7 | 14 | 1101 | 19 | 989 | -133.55 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-03-05 | 13:03 | 0.1 | 0.3 | 19.6 | 0 | 3 | 80 | 983 | -147.48 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW23 | gas well 23 | 2021-03-05 | 13:04 | 0.3 | 0.4 | 20.3 | 0 | 0 | 79 | 983 | -129.55 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW23 | gas well 23 | 2021-03-09 | 11:35 | 1 | 1.1 | 20.2 | 17 | 4 | 77.7 | 971 | -175.02 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW23 | gas well 23 | 2021-03-09 | 11:35 | 0.7 | 0.8 | 19.1 | 22 | 7 | 79.4 | 971 | -0.56 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW23 | gas well 23 | 2021-03-09 | 11:36 | 1 | 1.2 | 20.2 | 17 | 4 | 77.6 | 971 | -1.11 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW23 | gas well 23 | 2021-03-16 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW23 | gas well 23 | 2021-03-26 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW23 | gas well 23 | 2021-03-30 | [13 empty] | 10 | GTE Line flooded | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW24 | gas well 24 | 2021-01-15 | [13 empty] | 10 | GTE Line flooded | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW24 | gas well 24 | 2021-01-22 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW24 | gas well 24 | 2021-01-27 | [13 empty] | 10 | GTE Line flooded | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW24 | gas well 24 | 2021-02-05 | [13 empty] | 10 | GTE Line flooded | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW24 | gas well 24 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW24 | gas well 24 | 2021-02-16 | [13 empty] | 10 | GTE Line flooded | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW24 | gas well 24 | 2021-02-26 | 13:29 | 51.5 | 29.3 | 2.2 | 13 | 1124 | 17 | 989 | -125.22 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW24 | gas well 24 | 2021-03-05 | 13:04 | 0 | 0.2 | 20.5 | 0 | 0 | 79.3 | 983 | -118.97 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW24 | gas well 24 | 2021-03-09 | 11:36 | 1.2 | 1.4 | 20.1 | 16 | 4 | 77.3 | 971 | -0.52 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW24 | gas well 24 | 2021-03-16 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW24 | gas well 24 | 2021-03-26 | [13 empty] | 10 | GTE Line flooded | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW24 | gas well 24 | 2021-03-30 | [13 empty] | 10 | GTE Line flooded | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW25 | gas well 25 | 2021-01-15 | 10:02 | 62.6 | 29.4 | 1.1 | 31 | 9 | 6.9 | 981 | -142.5 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW25 | gas well 25 | 2021-01-22 | 10:21 | 0.2 | 0.4 | 17.8 | 11 | 18 | 81.6 | 944 | -179.74 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-01-22 | 10:22 | 0.6 | 0.6 | 20.3 | 8 | 7 | 78.5 | 944 | -179.21 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-01-27 | 11:00 | 26.1 | 15.1 | 13.4 | 7 | 1 | 45.4 | 965 | -139.81 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW25 | gas well 25 | 2021-02-03 | 12:45 | 68.2 | 29.7 | 2 | 8 | 49 | 0.1 | 949 | -135.91 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-02-03 | 12:46 | 68.6 | 31.6 | 1.1 | 9 | 27 | 0 | 949 | -136.79 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW25 | gas well 25 | 2021-02-16 | 11:45 | 68.8 | 34.4 | 0.9 | 28 | 319 | 0 | 957 | -164.56 |  | 30 |  | Condition good |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-02-26 | 13:15 | 68.8 | 33.5 | 0.5 | 10 | 281 | 0 | 988 | -171.29 |  | 100 |  | Condition good |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-03-05 | [12 empty] | WELL TO HIGH TO REACH | 8 | Unable to find sample point | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW25 | gas well 25 | 2021-03-09 | 11:22 | 62.7 | 32.5 | 2.2 | 16 | 29 | 2.6 | 974 | -207.06 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW25 | gas well 25 | 2021-03-16 | [12 empty] | AREA FLOODED AND WELL TO HIGH | 1 | Location inaccessible | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW25 | gas well 25 | 2021-03-25 | 14:55 | 72.9 | 32.3 | 0.6 | 26 | 24 | 0 | 969 | -184.34 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW25 | gas well 25 | 2021-03-30 | 14:45 | 55.8 | 27.5 | 3.8 | 30 | 29 | 12.9 | 980 | -175.65 |  | 50 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW26 | gas well 26 | 2021-01-15 | 9:57 | 37.7 | 23.3 | 5.9 | 24 | 17 | 33.1 | 981 | -20.29 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW26 | gas well 26 | 2021-01-22 | 10:19 | 62.4 | 28.8 | 2.6 | 24 | 56 | 6.2 | 945 | -2.62 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW26 | gas well 26 | 2021-01-27 | 10:56 | 12.6 | 11.3 | 10.2 | 11 | 24 | 65.9 | 965 | -30.18 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW26 | gas well 26 | 2021-02-03 | 12:37 | 34.5 | 22.7 | 4.1 | 19 | 43 | 38.7 | 949 | -14.99 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW26 | gas well 26 | 2021-02-11 | [12 empty] | LINE ICY | 6 | No safe access | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW26 | gas well 26 | 2021-02-16 | 11:37 | 23.7 | 16.1 | 7 | 8 | 24 | 53.2 | 959 | -17.13 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW26 | gas well 26 | 2021-02-26 | 13:08 | 31.1 | 21 | 3.6 | 13 | 27 | 44.3 | 990 | -19.26 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW26 | gas well 26 | 2021-03-05 | 13:29 | 26.5 | 19.1 | 5.2 | 5 | 26 | 49.2 | 984 | -23.92 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW26 | gas well 26 | 2021-03-09 | 10:33 | 25.7 | 17.4 | 6.9 | 23 | 28 | 50 | 972 | -22.16 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW26 | gas well 26 | 2021-03-16 | 14:20 | 27.1 | 17.4 | 7.2 | 29 | 32 | 48.3 | 981 | -18.21 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW26 | gas well 26 | 2021-03-25 | 14:47 | 30 | 19.1 | 4.9 | 32 | 36 | 46 | 970 | -26.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW26 | gas well 26 | 2021-03-30 | 14:38 | 29.7 | 18.2 | 5.8 | 38 | 31 | 46.3 | 980 | -17.86 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW27 | gas well 27 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW27 | gas well 27 | 2021-01-22 | 10:23 | 43.8 | 28.7 | 2.6 | 15 | 37 | 24.9 | 944 | -0.31 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW27 | gas well 27 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW27 | gas well 27 | 2021-02-03 | 12:38 | 43.4 | 28.5 | 1.1 | 19 | 59 | 27 | 948 | -0.83 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW27 | gas well 27 | 2021-02-11 | [12 empty] | LINER ICY | 6 | No safe access | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW27 | gas well 27 | 2021-02-16 | 11:38 | 40.7 | 27.1 | 1.6 | 12 | 37 | 30.6 | 958 | -0.14 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW27 | gas well 27 | 2021-02-26 | 13:10 | 35.6 | 25.1 | 1.2 | 13 | 30 | 38.1 | 990 | 0.1 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW27 | gas well 27 | 2021-03-05 | 13:31 | 46.5 | 28.5 | 0.5 | 10 | 58 | 24.5 | 984 | -0.73 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW27 | gas well 27 | 2021-03-09 | 10:35 | 48.5 | 28.7 | 0.8 | 28 | 54 | 22 | 972 | -0.49 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW27 | gas well 27 | 2021-03-16 | 14:21 | 46.1 | 27.1 | 1.1 | 33 | 55 | 25.7 | 980 | -0.31 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW27 | gas well 27 | 2021-03-25 | 14:49 | 53 | 29.3 | 0.8 | 36 | 66 | 16.9 | 968 | -0.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW27 | gas well 27 | 2021-03-30 | 14:40 | 41.5 | 25.3 | 1.4 | 41 | 30 | 31.8 | 979 | -0.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW28 | gas well 28 | 2021-01-07 | 15:36 | 65.5 | 34.5 | 0.9 | 20 | 3 | 0 | 968 | -139.69 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW28 | gas well 28 | 2021-01-15 | 10:09 | 57.8 | 35.3 | 0.9 | 31 | 1 | 6 | 979 | -143.37 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW28 | gas well 28 | 2021-01-22 | 10:28 | 71.3 | 33.1 | 0 | 13 | 2008 | 0 | 944 | -179.24 |  | 100 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW28 | gas well 28 | 2021-01-27 | 11:01 | 68.2 | 31.8 | 0.9 | 11 | 1583 | 0 | 964 | -133.44 |  | 100 |  | Condition good |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW28 | gas well 28 | 2021-02-03 | 12:44 | 70.5 | 33.1 | 0.1 | 14 | 1856 | 0 | 947 | -132.4 |  | 100 |  | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW28 | gas well 28 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW28 | gas well 28 | 2021-02-16 | 11:41 | 70.3 | 32.8 | 0.2 | 10 | 1335 | 0 | 958 | -165.03 |  | 100 |  | Condition good |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW28 | gas well 28 | 2021-02-26 | 13:12 | 69.9 | 32 | 0.2 | 13 | 1175 | 0 | 989 | -169.52 |  | 100 |  | Condition good |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW28 | gas well 28 | 2021-03-05 | 13:34 | 70.3 | 32.7 | 0.4 | 9 | 737 | 0 | 983 | -200.41 |  | 100 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW28 | gas well 28 | 2021-03-09 | 11:19 | 71.4 | 32.1 | 0.7 | 17 | 961 | 0 | 971 | -207.84 |  | 100 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW28 | gas well 28 | 2021-03-16 | 14:24 | 70.1 | 32.1 | 0.5 | 31 | 866 | 0 | 981 | -194.11 |  | 100 |  | Condition good |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW28 | gas well 28 | 2021-03-25 | 14:52 | 71 | 32.1 | 0.2 | 33 | 810 | 0 | 968 | -180.87 |  | 100 |  | Condition good |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW28 | gas well 28 | 2021-03-30 | 14:43 | 69.5 | 31.2 | 0.1 | 40 | 901 | 0 | 979 | -173.79 |  | 100 |  | Condition good |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW29 | gas well 29 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW29 | gas well 29 | 2021-01-22 | 10:25 | 62.1 | 39.1 | 0.7 | 18 | 52 | 0 | 945 | -66.12 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW29 | gas well 29 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW29 | gas well 29 | 2021-02-03 | 12:40 | 62.2 | 38 | 0.3 | 22 | 71 | 0 | 947 | -47.45 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW29 | gas well 29 | 2021-02-11 | [12 empty] | LINER ICY | 6 | No safe access | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW29 | gas well 29 | 2021-02-16 | 11:40 | 62.1 | 38.4 | 0.6 | 15 | 47 | 0 | 958 | -60.1 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW29 | gas well 29 | 2021-02-26 | 13:11 | 60.9 | 36.5 | 0.3 | 17 | 34 | 2.3 | 989 | -25.3 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW29 | gas well 29 | 2021-03-05 | 13:32 | 61.8 | 37.3 | 0.6 | 13 | 49 | 0.3 | 983 | -37.73 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW29 | gas well 29 | 2021-03-09 | 10:36 | 64.4 | 38.2 | 0.2 | 32 | 44 | 0 | 972 | -37.19 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW29 | gas well 29 | 2021-03-16 | 14:22 | 65.3 | 38.6 | 0.4 | 37 | 37 | 0 | 981 | -22.96 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW29 | gas well 29 | 2021-03-25 | 14:50 | 64.8 | 38.1 | 0.2 | 41 | 48 | 0 | 968 | -23.34 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW29 | gas well 29 | 2021-03-30 | 14:41 | 61.5 | 36.4 | 0.1 | 50 | 50 | 2 | 979 | -15.74 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-01-04 | 15:10 | 37.8 | 28 | 8 | 20 | 0 | 26.2 | 971 | -1.7 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-01-04 | 15:10 | 36.9 | 27.7 | 6.9 | 20 | 0 | 28.5 | 971 | -1.94 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-01-15 | 9:46 | 0.8 | 0.5 | 18.8 | 27 | 32 | 79.9 | 981 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW30 | 30m deep steel well 1st | 2021-01-22 | 10:09 | 0.3 | 0.5 | 12.9 | 10 | 30 | 86.3 | 946 | -0.66 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW30 | 30m deep steel well 1st | 2021-01-27 | 10:27 | 0.3 | 0.3 | 17.1 | 55 | 48 | 82.3 | 965 | -0.19 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-02-03 | 12:24 | 0.3 | 0.3 | 21 | 3 | 12 | 78.4 | 948 | -0.82 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW30 | 30m deep steel well 1st | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-02-16 | 11:09 | 0.5 | 0.4 | 20.8 | 17 | 11 | 78.3 | 959 | -1.15 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW30 | 30m deep steel well 1st | 2021-02-26 | 12:59 | 0 | 0.1 | 20.4 | 0 | 0 | 79.5 | 991 | -1.11 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW30 | 30m deep steel well 1st | 2021-03-05 | 13:15 | 0.2 | 0.2 | 20.8 | 29 | 13 | 78.8 | 984 | -0.94 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW30 | 30m deep steel well 1st | 2021-03-09 | 10:23 | 0.2 | 0.2 | 19.8 | 20 | 14 | 79.8 | 972 | -0.71 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW30 | 30m deep steel well 1st | 2021-03-16 | 14:10 | 0.2 | 0.2 | 20.8 | 25 | 14 | 78.8 | 981 | -2.55 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW30 | 30m deep steel well 1st | 2021-03-25 | 14:37 | 0.3 | 0.2 | 18.8 | 32 | 31 | 80.7 | 968 | -0.73 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW30 | 30m deep steel well 1st | 2021-03-30 | 14:26 | 0.1 | 0.1 | 20 | 33 | 13 | 79.8 | 979 | -0.83 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW31 | 30m deep steel well 2nd | 2021-01-04 | 15:12 | 45.2 | 36.1 | 2 | 56 | 45 | 16.7 | 971 | -7.83 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW31 | 30m deep steel well 2nd | 2021-01-15 | 9:48 | 51.8 | 37.8 | 1.4 | 74 | 79 | 9 | 981 | -6.35 |  | 20 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW31 | 30m deep steel well 2nd | 2021-01-22 | 10:11 | 48.2 | 38.4 | 1.5 | 56 | 66 | 11.9 | 946 | -7.83 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW31 | 30m deep steel well 2nd | 2021-01-27 | 10:26 | 50.7 | 38.3 | 1.2 | 63 | 95 | 9.8 | 964 | -5.29 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW31 | 30m deep steel well 2nd | 2021-02-03 | 12:26 | 52.7 | 39.3 | 1 | 89 | 73 | 7 | 948 | -3.92 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW31 | 30m deep steel well 2nd | 2021-02-11 | 11:04 | 42 | 34.9 | 2.6 | 56 | 19 | 20.5 | 973 | -7.22 |  | 20 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW31 | 30m deep steel well 2nd | 2021-02-16 | 10:50 | 51.6 | 38 | 0.8 | 74 | 82 | 9.6 | 958 | -6.63 |  | 20 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW31 | 30m deep steel well 2nd | 2021-02-26 | 13:00 | 49.6 | 35.2 | 1.7 | 55 | 35 | 13.5 | 990 | -6.98 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW31 | 30m deep steel well 2nd | 2021-03-05 | 13:13 | 43.3 | 34.7 | 1.6 | 65 | 59 | 20.4 | 983 | -8.8 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW31 | 30m deep steel well 2nd | 2021-03-09 | 10:24 | 48.5 | 35.7 | 1.8 | 74 | 54 | 14 | 972 | -7.76 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW31 | 30m deep steel well 2nd | 2021-03-16 | 14:11 | 47 | 34.4 | 1.6 | 83 | 42 | 17 | 981 | -7.81 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW31 | 30m deep steel well 2nd | 2021-03-25 | 14:38 | 51.9 | 36.9 | 1.6 | 83 | 44 | 9.6 | 969 | -6.56 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW31 | 30m deep steel well 2nd | 2021-03-30 | 14:29 | 48.6 | 34.7 | 2 | 89 | 36 | 14.7 | 980 | -6.23 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-01-04 | 15:24 | 58.8 | 42 | 0.7 | 36 | 73 | 0 | 971 | -2.46 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-01-15 | 10:16 | 65.9 | 44 | 0.5 | 36 | 124 |  | 980 | -0.09 |  | 20 |  | Condition good |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW32 | 30m deep steel well 3rd | 2021-01-22 | 10:36 | 60 | 43 | 0.5 | 28 | 87 | 0 | 945 | -1.21 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-01-27 | 10:18 | 64.9 | 43.8 | 0.7 | 41 | 133 | 0 | 964 | -0.35 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-02-03 | 12:56 | 62.4 | 44.4 | 0.2 | 35 | 171 | 0 | 948 | -0.17 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-02-16 | 10:44 | 62.7 | 43.6 | 0.3 | 35 | 99 | 0 | 959 | -1.16 |  | 20 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-02-26 | 13:22 | 65 | 42.7 | 0.2 | 26 | 119 | 0 | 989 | -3.11 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-03-05 | 13:08 | 34.6 | 31.1 | 1.5 | 10 | 12 | 32.8 | 983 | -6.47 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-03-05 | 13:09 | 37.4 | 32.3 | 1.3 | 26 | 41 | 29 | 983 | -6.23 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW32 | 30m deep steel well 3rd | 2021-03-09 | 11:30 | 63.5 | 41.3 | 0.3 | 42 | 95 | 0 | 972 | -0.45 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW32 | 30m deep steel well 3rd | 2021-03-16 | 14:31 | 64.4 | 42.2 | 0.4 | 46 | 79 | 0 | 981 | -0.19 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW32 | 30m deep steel well 3rd | 2021-03-25 | 15:00 | 65 | 43.4 | 0.1 | 51 | 112 | 0 | 962 | -0.47 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-03-25 | 15:01 | 65.6 | 43.8 | 0 | 61 | 164 | 0 | 962 | -0.47 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW32 | 30m deep steel well 3rd | 2021-03-30 | 14:52 | 63.4 | 42.4 | 0 | 73 | 86 | 0 | 979 | -0.03 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-01-04 | 15:25 | 50.4 | 31.9 | 3.4 | 39 | 53 | 14.3 | 971 | -11.16 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-01-15 | 10:17 | 54.7 | 30.6 | 3.9 | 38 | 56 | 10.8 | 981 | -7.03 |  | 20 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW33 | 30m deep steel well 4th | 2021-01-22 | 10:38 | 52.2 | 32.2 | 3.2 | 32 | 27 | 12.4 | 945 | -11.78 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-01-27 | 10:16 | 50.6 | 30.5 | 3.5 | 6 | 72 | 15.4 | 964 | -9.63 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-02-03 | 13:00 | 53.2 | 32.6 | 3.5 | 40 | 39 | 10.7 | 947 | -8.66 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-02-16 | 10:39 | 50.9 | 32 | 3 | 8 | 8 | 14.1 | 958 | -9.37 |  | 30 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-02-26 | 13:23 | 49.7 | 29.6 | 3.6 | 31 | 62 | 17.1 | 989 | -7.84 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-05 | 13:06 | 32.2 | 25.1 | 4.4 | 0 | 0 | 38.3 | 984 | -15.32 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-03-05 | 13:06 | 31 | 24.8 | 4.5 | 0 | 0 | 39.7 | 984 | -0.54 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW33 | 30m deep steel well 4th | 2021-03-09 | 11:31 | 67.3 | 35.9 | 0.1 | 48 | 42 | 0 | 972 | -0.36 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-09 | 11:33 | 57 | 31.4 | 2.6 | 42 | 13 | 9 | 972 | -3.11 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-09 | 11:33 | 56.2 | 31.5 | 2.7 | 39 | 13 | 9.6 | 972 | -0.64 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-16 | 14:33 | 69.4 | 36.5 | 0.2 | 58 | 48 | 0 | 981 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-25 | 15:04 | 69.5 | 36.5 | 0.3 | 64 | 25 | 0 | 967 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-25 | 15:05 | 64.8 | 33.2 | 1.4 | 57 | 17 | 0.6 | 967 | -2.24 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW33 | 30m deep steel well 4th | 2021-03-30 | 14:54 | 52.6 | 29.3 | 2.8 | 49 | 19 | 15.3 | 980 | -6.8 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-01-15 | 10:41 | 58.2 | 32.5 | 0.9 | 28 | 10 | 8.4 | 980 | -95.35 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW34 | 30m deep steel well 5th | 2021-01-22 | 10:40 | 65.7 | 36.6 | 0.6 | 27 | 16 | 0 | 946 | -141.63 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-02-03 | 13:02 | 62.2 | 35.9 | 0.5 | 34 | 12 | 1.4 | 948 | -87.03 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-02-08 | 13:22 | 39.5 | 27.9 | 8.4 | 17 | 469 | 24.2 | 955 | -185.12 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-02-16 | 10:38 | 54.2 | 32.3 | 0.4 | 10 | 50 | 13.1 | 958 | -160.08 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-02-26 | 13:30 | 51.2 | 31.2 | 0.7 | 12 | 109 | 16.9 | 990 | -132.11 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-05 | 12:54 | 44.2 | 29.2 | 0.8 | 0 | 0 | 25.8 | 983 | -145.66 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-03-05 | 12:55 | 44.1 | 29.4 | 0.5 | 1 | 0 | 26 | 983 | -149.43 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-03-09 | 11:42 | 44.3 | 29.7 | 0.2 | 22 | 43 | 25.8 | 971 | -164.04 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-16 | 14:37 | 53.9 | 32 | 0.4 | 34 | 47 | 13.7 | 981 | -159.87 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-25 | 13:09 | 49.9 | 30.9 | 0.4 | 32 | 11 | 18.8 | 969 | 2.2 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-25 | 13:10 | 64.1 | 35.9 | 0.1 | 27 | 16 | 0 | 969 | -78.74 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-25 | 13:11 | 55.6 | 33.9 | 0.1 | 25 | 22 | 10.4 | 969 | -142.07 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-25 | 0.55069 | 52.5 | 32.5 | 0.1 | 24 | 17 | 14.9 | 969 | -86.5 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW34 | 30m deep steel well 5th | 2021-03-30 | 13:19 | 58 | 33.1 | 0.2 | 40 | 20 | 8.7 | 980 | -168.62 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW34 | 30m deep steel well 5th | 2021-03-30 | 13:20 | 58.4 | 33.2 | 0.1 | 38 | 13 | 8.3 | 980 | -177.78 |  | 20 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW35 | GAS WELL 35 | 2021-01-15 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW35 | GAS WELL 35 | 2021-01-22 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW35 | GAS WELL 35 | 2021-01-27 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW35 | GAS WELL 35 | 2021-02-05 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW35 | GAS WELL 35 | 2021-02-11 | [12 empty] | AREA FLOODED/FROZEN | 6 | No safe access | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW35 | GAS WELL 35 | 2021-02-16 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW35 | GAS WELL 35 | 2021-02-26 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW35 | GAS WELL 35 | 2021-03-05 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW35 | GAS WELL 35 | 2021-03-08 | 15:05 | 45.4 | 31.7 | 5.1 | 7 | 9 | 17.8 | 975 | -25.96 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW35 | GAS WELL 35 | 2021-03-16 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW35 | GAS WELL 35 | 2021-03-26 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW35 | GAS WELL 35 | 2021-03-30 | [12 empty] | AREA FLOODED | 6 | No safe access | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-01-04 | 14:08 | 65 | 40.8 | 0.2 | 28 | 84 | 0 | 972 | -0.87 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-01-15 | 8:58 | 0.6 | 0.3 | 18.2 | 25 | 26 | 80.9 | 982 | -0.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW36 | GAS WELL 36 | 2021-01-18 | 15:14 | 69.6 | 43.3 | 0.7 | 34 | 82 |  | 970 | -0.38 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-01-25 | 14:55 | 64.6 | 43.6 | 0.8 | 29 | 94 | 0 | 965 | -0.31 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-02-01 | 15:10 | 25.6 | 17.6 | 12.3 | 16 | 21 | 44.5 | 952 | -63.41 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-02-08 | 13:57 | 64.2 | 42.3 | 0.1 | 23 | 114 | 0 | 956 | 259.66 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-02-08 | 13:59 | 65.1 | 41.7 | 0.3 | 19 | 105 | 0 | 956 | -0.19 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-02-15 | 15:34 | 38 | 25.8 | 8.5 | 29 | 68 | 27.7 | 969 | -54.42 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-02-15 | 15:35 | 35.9 | 24.8 | 8.5 | 28 | 69 | 30.8 | 969 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-02-22 | 15:02 | 56.3 | 38.1 | 1.7 | 31 | 72 | 3.9 | 969 | -22.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-03-02 | 14:58 | 39.2 | 26.6 | 7.2 | 23 | 23 | 27 | 981 | -83.04 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW36 | GAS WELL 36 | 2021-03-08 | 15:11 | 46.7 | 30.4 | 4.9 | 9 | 5 | 18 | 976 | -0.33 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW36 | GAS WELL 36 | 2021-03-16 | 12:58 | 46.3 | 31.5 | 5.3 | 40 | 37 | 16.9 | 982 | -28.39 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW36 | GAS WELL 36 | 2021-03-25 | 13:34 | 55.2 | 37 | 2.3 | 41 | 50 | 5.5 | 970 | -6.91 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW36 | GAS WELL 36 | 2021-03-30 | 13:37 | 48.2 | 31.9 | 4.3 | 42 | 19 | 15.6 | 981 | -9.61 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-01-04 | 14:12 | 62.5 | 41.5 | 0.9 | 22 | 24 | 0 | 973 | -36.98 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-01-15 | 9:02 | 64.7 | 40.2 | 0.8 | 28 | 22 | 0 | 983 | -92.55 |  | 20 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW37 | GAS WELL 37 | 2021-01-18 | 15:17 | 66.6 | 42.1 | 0.8 | 29 | 59 | 0 | 972 | -76.66 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-01-25 | 14:58 | 63.6 | 40.6 | 0.4 | 24 | 59 | 0 | 966 | -3.92 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-02-01 | 15:15 | 62.6 | 43.2 | 0.2 | 17 | 78 | 0 | 952 | -0.23 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-02-15 | 15:36 | 59.7 | 40.6 | 0.3 | 27 | 66 | 0 | 969 | -35.42 |  | 30 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-02-22 | 15:04 | 61.2 | 41.4 | 0.1 | 27 | 105 | 0 | 970 | -37.02 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-03-02 | 15:06 | 59.2 | 39 | 0.4 | 16 | 39 | 1.4 | 980 | -78.95 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-03-08 | 15:13 | 60.5 | 37.8 | 0.6 | 8 | 4 | 1.1 | 976 | -50.26 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW37 | GAS WELL 37 | 2021-03-16 | 13:02 | 47.9 | 32.2 | 4.2 | 28 | 11 | 15.7 | 982 | -98.32 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW37 | GAS WELL 37 | 2021-03-25 | 13:39 | 41.7 | 28.7 | 6.6 | 27 | 6 | 23 | 970 | -89.57 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-03-25 | 13:39 | 40.1 | 28.1 | 6.7 | 26 | 5 | 25.1 | 970 | -57.2 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW37 | GAS WELL 37 | 2021-03-30 | 13:39 | 57.4 | 44.1 | 0.5 | 38 | 71 | 0 | 982 | 132.21 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW37 | GAS WELL 37 | 2021-03-30 | 13:41 | 57.5 | 44.1 | 0.1 | 46 | 92 | 0 | 982 | 2.78 |  | 20 |  | Investigation/attention required |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-01-04 | 14:13 | 60.8 | 38 | 1.6 | 25 | 32 | 0 | 972 | -150.55 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-01-15 | 9:04 | 63.5 | 38.4 | 1.4 | 28 | 50 | 0 | 982 | -129.45 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW38 | GAS WELL 38 | 2021-01-18 | 15:26 | 60.2 | 37.5 | 2 | 25 | 57 | 0.3 | 970 | -129.83 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-01-25 | 15:00 | 59.6 | 39.1 | 1.2 | 21 | 53 | 0.1 | 965 | -157.22 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-02-01 | 15:17 | 58.8 | 39.6 | 1.2 | 19 | 42 | 0.4 | 952 | -157.5 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-02-08 | 14:02 | 61.9 | 40.1 | 1.5 | 17 | 52 | 0 | 956 | -189.74 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-02-15 | 15:38 | 61.9 | 39.6 | 0.4 | 29 | 46 | 0 | 969 | -178.74 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-02-22 | 15:07 | 58.7 | 37.5 | 1.2 | 22 | 37 | 2.6 | 970 | -160.55 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-03-02 | 15:07 | 58.9 | 36.8 | 1.3 | 18 | 25 | 3 | 981 | -207.79 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-03-08 | 15:27 | 29.8 | 27 | 9.2 | 6 | 2 | 34 | 976 | -190.3 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW38 | GAS WELL 38 | 2021-03-08 | 15:27 | 29.6 | 24.8 | 9.6 | 6 | 2 | 36 | 976 | -167.13 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW38 | GAS WELL 38 | 2021-03-16 | 13:04 | 60.9 | 40.6 | 0.2 | 32 | 43 | 0 | 982 | 221.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW38 | GAS WELL 38 | 2021-03-16 | 13:04 | 57.5 | 39.6 | 1 | 31 | 50 | 1.9 | 982 | -179.15 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW38 | GAS WELL 38 | 2021-03-16 | 13:05 | 57.2 | 38.5 | 1.3 | 31 | 44 | 3 | 982 | -148.11 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW38 | GAS WELL 38 | 2021-03-25 | 13:41 | 58.6 | 37.8 | 1.1 | 31 | 25 | 2.5 | 969 | -166.83 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-03-25 | 13:41 | 57.8 | 37.6 | 1.2 | 31 | 37 | 3.4 | 969 | -167.32 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW38 | GAS WELL 38 | 2021-03-30 | 13:42 | 58.2 | 42.2 | 0.5 | 49 | 44 | 0 | 981 | -170.36 |  | 30 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW38 | GAS WELL 38 | 2021-03-30 | 13:43 | 57.9 | 41.8 | 0.3 | 50 | 28 | 0 | 981 | -175.02 |  | 40 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW39 | GAS WELL 39 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW39 | GAS WELL 39 | 2021-01-18 | 15:28 | 65.3 | 41.2 | 0.6 | 24 | 38 | 0 | 970 | -113.36 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW39 | GAS WELL 39 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW39 | GAS WELL 39 | 2021-02-01 | 15:18 | 62 | 42.6 | 0.6 | 16 | 33 | 0 | 953 | -131.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW39 | GAS WELL 39 | 2021-02-08 | 14:04 | 62 | 41.8 | 0.9 | 15 | 25 | 0 | 956 | -170.18 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW39 | GAS WELL 39 | 2021-02-15 | 15:40 | 62.1 | 41 | 0.2 | 26 | 38 | 0 | 969 | -100.5 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW39 | GAS WELL 39 | 2021-02-22 | 15:08 | 61 | 40.6 | 0.4 | 19 | 27 | 0 | 969 | -92.64 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW39 | GAS WELL 39 | 2021-03-02 | 15:09 | 61.3 | 40.4 | 0.3 | 15 | 17 | 0 | 981 | -66.89 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW39 | GAS WELL 39 | 2021-03-08 | 15:29 | 61.6 | 33.9 | 0.5 | 6 | 2 | 4 | 975 | -111.37 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW39 | GAS WELL 39 | 2021-03-16 | 13:07 | 60.9 | 40.4 | 0.2 | 29 | 22 | 0 | 982 | -94.55 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW39 | GAS WELL 39 | 2021-03-25 | 13:43 | 61.9 | 40.9 | 0.2 | 28 | 24 | 0 | 970 | -92.31 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW39 | GAS WELL 39 | 2021-03-30 | 13:44 | 59.5 | 41.8 | 0.2 | 44 | 22 | 0 | 981 | -94.62 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-01-04 | 13:48 | 52.2 | 35.6 | 0.8 | 45 | 29 | 11.4 | 971 | -37.17 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-01-15 | 8:36 | 65 | 40.8 | 0.5 | 45 | 41 | 0 | 980 | -24.07 |  | 35 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW40 | WELL 40 | 2021-01-18 | 14:39 | 63.9 | 39.7 | 0.1 | 46 | 40 | 0 | 970 | -26.92 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-01-25 | 14:32 | 57.5 | 39.8 | 0.7 | 43 | 37 | 2 | 965 | -29.35 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-02-01 | 14:30 | 59.3 | 40.4 | 0.3 | 37 | 54 | 0 | 951 | -26.29 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-02-15 | 14:37 | 60.2 | 39.4 | 0.1 | 48 | 26 | 0.3 | 969 | -25.23 |  | 35 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-02-22 | 14:33 | 54.9 | 37.5 | 0.3 | 38 | 27 | 7.3 | 968 | -23.01 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-03-02 | 14:18 | 60.1 | 39.1 | 0.3 | 30 | 17 | 0.5 | 983 | -15.43 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-03-08 | 14:19 | 61 | 38.8 | 0.5 | 40 | 36 | 0 | 978 | -16.7 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW40 | WELL 40 | 2021-03-15 | 15:08 | 60.6 | 38.6 | 0.2 | 39 | 55 | 0.6 | 977 | -19.11 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW40 | WELL 40 | 2021-03-15 | 15:09 | 60.9 | 39.9 | 0.1 | 43 | 99 | 0 | 977 | -78.24 |  | 40 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW40 | WELL 40 | 2021-03-25 | 12:56 | 33.8 | 27.6 | 1.1 | 30 | 6 | 37.5 | 970 | -96.58 |  | 40 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-03-25 | 12:58 | 33.7 | 28.5 | 0.8 | 32 | 10 | 37 | 970 | -46.3 |  | 30 |  | Investigation/attention required |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-03-25 | 12:58 | 33.3 | 28.8 | 0.9 | 26 | 9 | 37 | 970 | -14.84 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW40 | WELL 40 | 2021-03-30 | 13:00 | 63.5 | 43.2 | 0.1 | 64 | 239 | 0 | 980 | -5.92 |  | 30 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW40 | WELL 40 | 2021-03-30 | 13:00 | 61.9 | 41.1 | 0.4 | 56 | 98 | 0 | 980 | 7.08 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW41 | WELL 41 | 2021-01-04 | 13:46 | 56.3 | 36 | 0.8 | 60 | 6 | 6.9 | 969 | -149.96 |  | 40 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW41 | WELL 41 | 2021-01-15 | 8:35 | 63.5 | 43.9 | 0.4 | 66 | 13 | 0 | 981 | -0.02 |  | 40 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW41 | WELL 41 | 2021-01-18 | 14:38 | 53.3 | 34.3 | 0.7 | 57 | 10 | 11.7 | 970 | -130.34 |  | 40 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-01-25 | 14:30 | 56.6 | 38.9 | 0.2 | 63 | 9 | 4.3 | 965 | -123.53 |  | 40 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW41 | WELL 41 | 2021-02-01 | 0.60347 | 59.7 | 41.4 | 0.4 | 57 | 12 | 0 | 951 | -118.46 |  | 40 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW41 | WELL 41 | 2021-02-15 | 14:36 | 56 | 36.5 | 0.8 | 65 | 19 | 6.7 | 969 | -141.53 |  | 40 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-02-22 | 0.60556 | 51.7 | 35.2 | 0.5 | 55 | 5 | 12.6 | 968 | -165.72 |  | 40 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-03-02 | 14:17 | 43.1 | 32.7 | 2 | 52 | 4 | 22.2 | 980 | -155.12 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW41 | WELL 41 | 2021-03-08 | 0.59375 | 37.5 | 28.3 | 4.7 | 55 | 6 | 29.5 | 977 | -190.68 |  | 40 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW41 | WELL 41 | 2021-03-08 | 14:16 | 37.1 | 28.5 | 4.1 | 55 | 7 | 30.3 | 977 | -194.7 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW41 | WELL 41 | 2021-03-15 | 15:05 | 48.1 | 22.4 | 4.9 | 41 | 7 | 24.6 | 976 | 72.2 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW41 | WELL 41 | 2021-03-15 | 0.62986 | 46.8 | 21.3 | 4.9 | 32 | 4 | 27 | 976 | -0.33 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW41 | WELL 41 | 2021-03-25 | 12:53 | 59.8 | 21.8 | 2.6 | 36 | 7 | 15.8 | 972 | 120.2 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-03-25 | 12:54 | 59.6 | 22 | 2.4 | 31 | 5 | 16 | 972 | -54.79 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW41 | WELL 41 | 2021-03-30 | 12:58 | 51.6 | 27.7 | 3.9 | 55 | 9 | 16.8 | 982 | -167.54 |  | 20 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW42 | WELL 42 | 2021-01-04 | 13:45 | 62.9 | 45.1 | 0.6 | 66 | 7 | 0 | 972 | -136.11 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW42 | WELL 42 | 2021-01-15 | 8:34 | 67.3 | 45.7 | 0.5 | 70 | 10 |  | 980 | -90.91 |  | 100 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW42 | WELL 42 | 2021-01-18 | 14:37 | 63.5 | 43.7 | 0.6 | 63 | 15 | 0 | 969 | -117.09 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW42 | WELL 42 | 2021-01-25 | 14:28 | 62.1 | 40.1 | 0.6 | 51 | 19 | 0 | 965 | -120.93 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW42 | WELL 42 | 2021-02-01 | 0.60278 | 66 | 46.2 | 0.5 | 61 | 25 |  | 951 | -112.39 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW42 | WELL 42 | 2021-02-08 | 13:14 | 64.2 | 44.2 | 0.7 | 68 | 30 | 0 | 956 | -175.41 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW42 | WELL 42 | 2021-02-15 | 14:35 | 65.2 | 45.3 | 0.4 | 77 | 58 |  | 969 | -121.47 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW42 | WELL 42 | 2021-02-22 | 14:30 | 63 | 44.3 | 0.5 | 60 | 5 | 0 | 967 | -142.45 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW42 | WELL 42 | 2021-03-02 | 14:15 | 63.3 | 44.1 | 0.3 | 64 | 8 | 0 | 980 | -142.4 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW42 | WELL 42 | 2021-03-08 | 14:14 | 64.2 | 43.9 | 0.7 | 80 | 9 | 0 | 977 | -183.04 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW42 | WELL 42 | 2021-03-15 | 15:04 | 62.6 | 43.7 | 0.3 | 62 | 12 | 0 | 977 | -173.97 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW42 | WELL 42 | 2021-03-25 | 12:52 | 66.5 | 43.9 | 0.9 | 85 | 35 |  | 969 | -151.79 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW42 | WELL 42 | 2021-03-30 | 12:57 | 65.2 | 44.2 | 0.2 | 89 | 17 | 0 | 980 | -157.37 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-01-04 | 13:43 | 9.3 | 18 | 2.3 | 31 | 6 | 70.4 | 972 | -136.55 |  | 50 |  | Investigation/attention required |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-01-04 | 13:43 | 8.9 | 17.8 | 1.4 | 27 | 4 | 71.9 | 972 | -36.86 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-01-15 | 8:32 | 1.1 | 1.3 | 19.7 | 7 | 2 | 77.9 | 981 | 5.33 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW43 | WELL 43 | 2021-01-18 | 14:32 | 85.8 | 25.5 | 0.3 | 30 | 11 |  | 970 | 7.2 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-01-18 | 14:33 | 89.1 | 24.6 | 0.1 | 24 | 8 |  | 970 | -24.3 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-01-25 | 14:27 | 39.9 | 15.7 | 8.9 | 4 | 0 | 35.5 | 965 | -136.74 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-01-25 | 14:27 | 38.9 | 14.7 | 8.9 | 2 | 0 | 37.5 | 965 | -137.21 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-02-01 | 14:23 | 74.3 | 25.2 | 0.6 | 8 | 2 | 0 | 952 | 22.27 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-02-01 | 14:24 | 77.4 | 23.9 | 0.2 | 5 | 0 | 0 | 952 | -107.9 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-02-15 | 14:31 | 33.9 | 20.6 | 0.1 | 20 | 12 | 45.4 | 965 | -117.68 |  | 20 |  | Investigation/attention required |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-02-15 | 14:31 | 32.8 | 20.1 | 0.1 | 18 | 12 | 47 | 965 | -67.48 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-02-22 | 14:25 | 73.5 | 13.6 | 0.1 | 7 | 5 | 12.8 | 969 | 49.31 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-02-22 | 14:26 | 71.6 | 13.1 | 0.1 | 4 | 3 | 15.2 | 969 | -76.8 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-03-02 | 14:07 | 21.1 | 6.9 | 11.4 | 12 | 0 | 60.6 | 981 | -199.89 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-03-02 | 14:07 | 20.4 | 6.7 | 13.5 | 5 | 0 | 59.4 | 981 | -200.35 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-03-08 | 14:05 | 85 | 19 | 0.1 | 21 | 3 | 0 | 976 | -37.21 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW43 | WELL 43 | 2021-03-08 | 14:05 | 77.7 | 20.2 | 0.4 | 24 | 4 | 1.7 | 976 | -0.14 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW43 | WELL 43 | 2021-03-15 | 14:45 | 41.4 | 22.3 | 0.2 | 22 | 8 | 36.1 | 977 | -176.97 |  | 20 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW43 | WELL 43 | 2021-03-15 | 14:45 | 40.5 | 21.9 | 0.2 | 19 | 7 | 37.4 | 977 | -176.13 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW43 | WELL 43 | 2021-03-25 | 12:48 | 88 | 20 | 0.1 | 22 | 7 | 0 | 970 | -21.75 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-03-25 | 12:48 | 85.2 | 21 | 0.2 | 24 | 8 | 0 | 970 | -0.26 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW43 | WELL 43 | 2021-03-30 | 12:53 | 29.2 | 25.9 | 0.2 | 22 | 6 | 44.7 | 981 | -5.57 |  | 20 |  | Investigation/attention required |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW43 | WELL 43 | 2021-03-30 | 12:54 | 27.1 | 24.7 | 0.1 | 18 | 6 | 48.1 | 981 | -2.46 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW44 | WELL 44 | 2021-01-04 | 13:42 | 50.4 | 36.1 | 3.6 | 32 | 9 | 9.9 | 972 | -3.16 |  | 35 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW44 | WELL 44 | 2021-01-15 | 8:31 | 54.5 | 38.4 | 3 | 36 | 9 | 4.1 | 981 | -0.03 |  | 30 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW44 | WELL 44 | 2021-01-18 | 14:31 | 64.9 | 44.3 | 0.2 | 46 | 14 | 0 | 970 | -0.02 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-01-25 | 0.60139 | 42.3 | 31.3 | 6 | 14 | 3 | 20.4 | 966 | -12.18 |  | 35 |  | Odour/migration control |  |  | No | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW44 | WELL 44 | 2021-02-01 | 14:21 | 43.4 | 31.7 | 5.8 | 15 | 5 | 19.1 | 952 | -11.91 |  | 35 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-02-01 | 14:22 | 47.1 | 34.6 | 4.5 | 20 | 2 | 13.8 | 952 | -6.21 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW44 | WELL 44 | 2021-02-15 | 14:28 | 59.1 | 42.7 | 0.2 | 34 | 24 | 0 | 963 | -0.23 |  | 30 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-02-15 | 14:30 | 62 | 43.1 | 0.1 | 40 | 28 | 0 | 963 | -4.96 |  | 35 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-02-22 | 14:24 | 59 | 41.6 | 0.4 | 26 | 17 | 0 | 969 | -0.1 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-03-02 | 14:05 | 62 | 38.7 | 0.3 | 25 | 1 | 0 | 981 | -6.65 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW44 | WELL 44 | 2021-03-08 | 14:03 | 48.9 | 34.7 | 4 | 36 | 4 | 12.4 | 976 | -4.88 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW44 | WELL 44 | 2021-03-15 | 14:43 | 51.4 | 35.7 | 3.3 | 40 | 13 | 9.6 | 977 | -5.95 |  | 30 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW44 | WELL 44 | 2021-03-25 | 12:47 | 55.6 | 39 | 2 | 39 | 10 | 3.4 | 970 | -2.45 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW44 | WELL 44 | 2021-03-30 | 12:52 | 54.8 | 38.7 | 1.8 | 40 | 6 | 4.7 | 981 | -2.55 |  | 30 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW45 | WELL 45 | 2021-01-04 | 13:40 | 48.3 | 34.7 | 0.6 | 18 | 12 | 16.4 | 972 | -60.55 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW45 | WELL 45 | 2021-01-15 | 8:27 | 55.4 | 35.4 | 0.7 | 17 | 4 | 8.5 | 981 | -47.57 |  | 35 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW45 | WELL 45 | 2021-01-18 | 14:28 | 54.8 | 36.1 | 0.2 | 29 | 12 | 8.9 | 971 | -51.46 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-01-25 | 14:24 | 47.2 | 34.8 | 0.3 | 7 | 7 | 17.7 | 965 | -56.59 |  | 35 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW45 | WELL 45 | 2021-02-01 | 14:20 | 49.3 | 35.8 | 0.2 | 9 | 15 | 14.7 | 952 | -59.01 |  | 35 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-02-08 | 13:09 | 45.7 | 34.3 | 0.3 | 11 | 0 | 19.7 | 957 | -69.56 |  | 35 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW45 | WELL 45 | 2021-02-15 | 14:26 | 46.3 | 32.7 | 0.2 | 26 | 25 | 20.8 | 970 | -57.98 |  | 35 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-02-22 | 14:21 | 40.5 | 32.4 | 0.1 | 10 | 20 | 27 | 969 | -59.94 |  | 35 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-02-22 | 14:22 | 40.3 | 32.4 | 0.1 | 10 | 35 | 27.2 | 969 | -38.53 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-03-02 | 14:02 | 50.5 | 34 | 0.2 | 19 | 0 | 15.3 | 981 | -26.07 |  | 25 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW45 | WELL 45 | 2021-03-08 | 14:02 | 50.8 | 33.9 | 0.2 | 31 | 3 | 15.1 | 976 | -26.34 |  | 25 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW45 | WELL 45 | 2021-03-15 | 14:41 | 51.5 | 33.9 | 0.2 | 32 | 23 | 14.4 | 977 | -24.75 |  | 25 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW45 | WELL 45 | 2021-03-25 | 12:45 | 55.2 | 34.8 | 0.3 | 28 | 16 | 9.7 | 970 | -24.23 |  | 25 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW45 | WELL 45 | 2021-03-30 | 12:50 | 52.7 | 35 | 0.3 | 30 | 5 | 12 | 981 | -23.22 |  | 25 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-01-08 | 12:53 | 59.9 | 41.4 | 0.3 | 78 | 14 | 0 | 969 | -1.06 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-01-08 | 12:54 | 49.4 | 35.4 | 1.1 | 69 | 9 | 14.1 | 969 | -1.54 |  | 35 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-01-08 | 12:55 | 48.8 | 35 | 1.1 | 71 | 8 | 15.1 | 969 | -1.08 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW46 | WELL 46 | 2021-01-18 | 14:34 | 39.3 | 30.6 | 1 | 34 | 4 | 29.1 | 970 | -0.1 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-01-18 | 14:35 | 38.5 | 30.4 | 0.9 | 34 | 3 | 30.2 | 970 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-01-29 | 15:02 | 69.8 | 46.9 | 0.6 | 62 | 52 |  | 952 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-01-29 | 15:03 | 57 | 40.6 | 1 | 62 | 40 | 1.4 | 952 | -0.43 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-01-29 | 15:04 | 56.5 | 41 | 0.8 | 57 | 34 | 1.7 | 952 | 0.45 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-02-01 | 14:26 | 67.6 | 41.3 | 0.7 | 55 | 27 | 0 | 951 | 0.02 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-02-08 | 13:13 | 63.2 | 43.7 | 0.5 | 62 | 31 | 0 | 955 | 0.02 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-02-15 | 14:33 | 63.6 | 41 | 0.1 | 76 | 75 | 0 | 969 | 0.26 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-02-22 | 14:28 | 52.3 | 37.7 | 0.8 | 57 | 0 | 9.2 | 968 | -0.66 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-03-02 | 14:13 | 51.1 | 39.1 | 0.6 | 46 | 12 | 9.2 | 981 | 0.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW46 | WELL 46 | 2021-03-08 | 14:07 | 68.7 | 43.7 | 0.1 | 88 | 15 |  | 975 | -0.31 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW46 | WELL 46 | 2021-03-08 | 14:09 | 65.4 | 42.7 | 0.4 | 88 | 18 | 0 | 975 | -0.21 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW46 | WELL 46 | 2021-03-15 | 14:49 | 25.4 | 21.4 | 5.3 | 32 | 4 | 47.9 | 976 | -0.12 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW46 | WELL 46 | 2021-03-15 | 14:49 | 23.6 | 21 | 5.4 | 32 | 5 | 50 | 976 | 0.17 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW46 | WELL 46 | 2021-03-25 | 12:50 | 70.3 | 44.3 | 0.1 | 89 | 36 |  | 970 | -0.43 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW46 | WELL 46 | 2021-03-30 | 12:55 | 68.7 | 43.6 | 0.2 | 76 | 15 |  | 980 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW47 | WELL 47 | 2021-01-04 | 13:53 | 60.1 | 44 | 0.7 | 47 | 33 | 0 | 972 | -153.73 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW47 | WELL 47 | 2021-01-15 | 8:38 | 62.9 | 39.9 | 0.5 | 30 | 57 | 0 | 981 | -90.51 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW47 | WELL 47 | 2021-01-18 | 15:04 | 63.2 | 44.9 | 0.6 | 67 | 82 | 0 | 970 | -129.87 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW47 | WELL 47 | 2021-01-25 | 14:34 | 59.9 | 45.1 | 0.5 | 44 | 72 | 0 | 966 | -138.58 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW47 | WELL 47 | 2021-02-01 | 14:53 | 61.1 | 45.7 | 0.4 | 53 | 140 | 0 | 952 | -118.05 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW47 | WELL 47 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW47 | WELL 47 | 2021-02-15 | 14:39 | 61.3 | 43.9 | 0.3 | 54 | 79 | 0 | 969 | -149.34 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW47 | WELL 47 | 2021-02-22 | 14:51 | 62.1 | 44.2 | 0.2 | 73 | 111 | 0 | 969 | -168.19 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW47 | WELL 47 | 2021-03-02 | 14:42 | 61.1 | 43.4 | 0.4 | 63 | 34 | 0 | 981 | -158.69 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW47 | WELL 47 | 2021-03-08 | 14:51 | 58.2 | 39.5 | 0.8 | 24 | 11 | 1.5 | 976 | -195.16 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW47 | WELL 47 | 2021-03-16 | 12:31 | 61.6 | 43 | 0.7 | 53 | 4 | 0 | 981 | -178.84 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW47 | WELL 47 | 2021-03-25 | 13:24 | 62.7 | 43.5 | 0.2 | 71 | 48 | 0 | 970 | -174.3 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW47 | WELL 47 | 2021-03-30 | 13:28 | 59.9 | 43.1 | 0.7 | 85 | 41 | 0 | 981 | -164.65 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-01-04 | 13:55 | 59.7 | 40.6 | 0.7 | 40 | 19 | 0 | 972 | -131.55 |  | 40 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-01-04 | 13:56 | 60.5 | 40.6 | 0.3 | 39 | 11 | 0 | 972 | -131.6 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-01-15 | 8:42 | 64 | 45.4 | 0.2 | 75 | 76 | 0 | 981 | -110.81 |  | 100 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR00GW48 | WELL 48 | 2021-01-18 | 14:44 | 67.4 | 41.4 | 0.2 | 40 | 634 | 0 | 969 | -118.31 |  | 100 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-01-25 | 14:36 | 59.3 | 40.3 | 0.9 | 36 | 30 | 0 | 965 | -134.86 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-02-01 | 14:35 | 55.6 | 35.2 | 0.9 | 22 | 91 | 8.3 | 951 | -117.11 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-02-15 | 14:41 | 55.3 | 37.1 | 0.5 | 45 | 35 | 7.1 | 969 | -143.7 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-02-22 | 14:38 | 11.1 | 8.4 | 16 | 11 | 34 | 64.5 | 968 | -154.63 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-02-22 | 14:38 | 10.9 | 8.3 | 15.6 | 15 | 101 | 65.2 | 968 | -154.84 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-03-02 | 14:23 | 67.3 | 39 | 0.1 | 29 | 445 | 0 | 980 | 71.99 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-03-02 | 14:24 | 67.2 | 39.3 | 0.1 | 28 | 529 | 0 | 980 | -184.74 |  | 50 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR00GW48 | WELL 48 | 2021-03-08 | 14:24 | 62.5 | 39 | 1.6 | 43 | 25 | 0 | 977 | -197.93 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW48 | WELL 48 | 2021-03-08 | 14:24 | 61.8 | 38.8 | 1.7 | 40 | 29 | 0 | 977 | -197.41 |  | 50 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR00GW48 | WELL 48 | 2021-03-16 | 12:33 | 50.3 | 34.3 | 1.1 | 45 | 5 | 14.3 | 981 | -180.87 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR00GW48 | WELL 48 | 2021-03-25 | 13:02 | 63.9 | 40.5 | 0.4 | 37 | 84 | 0 | 969 | -169.21 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR00GW48 | WELL 48 | 2021-03-30 | 13:09 | 0.7 | 0.5 | 19.5 | 26 | 88 | 79.3 | 980 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-01-04 | 14:27 | 61.8 | 40.2 | 0.9 | 26 | 21 | 0 | 972 | -158.68 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-01-07 | 16:11 | 62.6 | 40.1 | 0.9 | 19 | 34 | 0 | 970 | -133.09 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-01-15 | 9:10 | 46.4 | 33.4 | 1.5 | 29 | 52 | 18.7 | 981 | -135.06 |  | 100 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR010000 | MAnifold 1 | 2021-01-22 | 9:05 | 40.8 | 31.3 | 2.6 | 11 | 0 | 25.3 | 945 | -196.65 |  | 100 | 313 | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-01-25 | 15:26 | 60.3 | 40.8 | 0.2 | 9 | 37 | 0 | 965 | -161.04 |  | 100 | 213 | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-02-05 | 12:58 | 32.4 | 25.4 | 4 | 3 | 0 | 38.2 | 960 | -143.59 |  | 100 | 45 | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-02-05 | 13:12 | 57.7 | 38.6 | 1.6 | 8 | 18 | 2.1 | 960 | -152.69 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-02-08 | 14:16 | 52.6 | 35.5 | 4 | 10 | 16 | 7.9 | 958 | -198.8 |  | 100 | 386 | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-02-15 | 15:46 | 57.6 | 38.8 | 1.5 | 23 | 22 | 2.1 | 969 | -178.55 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-02-22 | 15:20 | 59.5 | 39.5 | 0.4 | 21 | 28 | 0.6 | 969 | -176.13 |  | 100 | 159 | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-03-03 | 13:09 | 59.3 | 39.1 | 0.7 | 7 | 0 | 0.9 | 980 | -205 |  | 100 | 67 | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR010000 | MAnifold 1 | 2021-03-09 | 9:37 | 39.5 | 28.1 | 4.9 | 13 | 0 | 27.5 | 974 | -200.9 |  | 100 | 149 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR010000 | MAnifold 1 | 2021-03-09 | 9:40 | 55.5 | 36.2 | 2.1 | 16 | 0 | 6.2 | 974 | -203.71 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR010000 | MAnifold 1 | 2021-03-16 | 13:20 | 59 | 38.7 | 0.4 | 31 | 22 | 1.9 | 982 | -188.04 |  | 100 | 78 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR010000 | MAnifold 1 | 2021-03-25 | 13:51 | 60.9 | 39.3 | 0.6 | 29 | 13 | 0 | 971 | -181.46 |  | 100 | 131 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR010000 | MAnifold 1 | 2021-03-30 | 13:50 | 57.3 | 38.1 | 0.5 | 41 | 27 | 4.1 | 980 | -174.59 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR010100 | MAN 1 LINE 1 | 2021-01-22 | 9:06 | 66.5 | 42.1 | 0.5 | 16 | 17 | 0 | 945 | -195.31 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR010100 | MAN 1 LINE 1 | 2021-02-05 | 12:59 | 61 | 39.9 | 0.4 | 12 | 33 | 0 | 960 | -142.26 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010100 | MAN 1 LINE 1 | 2021-03-03 | 13:10 | 59.2 | 39.1 | 0.5 | 9 | 0 | 1.2 | 979 | -204.79 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0101PN | M1 L1 pin well line | 2021-03-03 | 13:17 | 59.4 | 39.4 | 0.3 | 7 | 12 | 0.9 | 980 | -201.35 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0101SC | M1 L1 scavenger | 2021-03-03 | 13:23 | 59.3 | 38.7 | 0.5 | 1 | 0 | 1.5 | 979 | -0.03 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0101SC | M1 L1 scavenger | 2021-03-03 | 13:24 | 57 | 37.6 | 0.8 | 2 | 0 | 4.6 | 979 | -20.58 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0101SC | M1 L1 scavenger | 2021-03-09 | 9:39 | 18.1 | 16.8 | 9 | 12 | 0 | 56.1 | 973 | -14.82 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR0101SC | M1 L1 scavenger | 2021-03-09 | 9:39 | 17.8 | 16.6 | 9 | 11 | 0 | 56.6 | 973 | -10.53 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR010200 | MAN 1 LINE 2 | 2021-01-22 | 9:08 | 0.5 | 0.3 | 20.6 | 3 | 0 | 78.6 | 945 | -192.87 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR010200 | MAN 1 LINE 2 | 2021-01-22 | 9:08 | 0.5 | 0.3 | 19.3 | 4 | 0 | 79.9 | 945 | -194.13 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR010200 | MAN 1 LINE 2 | 2021-02-22 | 15:21 | 59.4 | 38.5 | 0.8 | 18 | 9 | 1.3 | 969 | -161.9 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR010200 | MAN 1 LINE 2 | 2021-02-22 | 15:22 | 58.1 | 38 | 1.1 | 18 | 7 | 2.8 | 969 | -175.49 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR010200 | MAN 1 LINE 2 | 2021-03-03 | 13:12 | 52.9 | 34.8 | 2.6 | 7 | 0 | 9.7 | 979 | -202.38 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR010300 | MAN 1 LINE 3 | 2021-01-22 | 9:11 | 40.2 | 30.9 | 3.4 | 12 | 3 | 25.5 | 945 | -192.64 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR010300 | MAN 1 LINE 3 | 2021-02-05 | 13:01 | 11.7 | 14.6 | 6.6 | 4 | 10 | 67.1 | 960 | -142.5 |  | 100 |  | Investigation/attention required |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010300 | MAN 1 LINE 3 | 2021-02-05 | 13:10 | 17.2 | 11.8 | 14.7 | 0 | 0 | 56.3 | 962 | -150.71 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010300 | MAN 1 LINE 3 | 2021-02-08 | 14:17 | 42.5 | 26.6 | 7.2 | 9 | 8 | 23.7 | 956 | -199.53 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR010300 | MAN 1 LINE 3 | 2021-03-03 | 13:13 | 37.6 | 24.9 | 7.5 | 4 | 0 | 30 | 979 | -201.11 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR010301 | M1 L3 pin wells | 2021-01-08 | 13:46 | 17.6 | 23.4 | 0.3 | 23 | 17 | 58.7 | 965 | -0.3 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010302 | M1 L3 pin wells | 2021-01-08 | 13:46 | 12 | 17 | 0.4 | 16 | 14 | 70.6 | 970 | -5.54 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010303 | M1 L3 pin wells | 2021-01-08 | 13:49 | 68 | 34.2 | 0.7 | 20 | 43 | 0 | 969 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010303 | M1 L3 pin wells | 2021-01-08 | 13:50 | 65.1 | 33.4 | 0.2 | 22 | 62 | 1.3 | 969 | -53.19 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010303 | M1 L3 pin wells | 2021-01-08 | 13:51 | 65.4 | 33.4 | 0.3 | 22 | 65 | 0.9 | 969 | -53.89 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010303 | M1 L3 pin wells | 2021-02-05 | 13:03 | 9.5 | 15.9 | 4.1 | 0 | 0 | 70.5 | 959 | -63.48 |  | 30 |  | Investigation/attention required |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010303 | M1 L3 pin wells | 2021-02-05 | 13:03 | 9 | 15.8 | 3.9 | 0 | 0 | 71.3 | 959 | -1.84 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010304 | M1 L4 pin wells | 2021-01-08 | 13:52 | 75.7 | 29.6 | 0.7 | 26 | 14 | 0 | 970 | -0.26 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010304 | M1 L4 pin wells | 2021-01-08 | 13:53 | 75.6 | 30 | 0 | 29 | 7 | 0 | 970 | -9.7 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010304 | M1 L4 pin wells | 2021-02-05 | 13:05 | 7.5 | 10 | 11.1 | 0 | 0 | 71.4 | 959 | -71.83 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010304 | M1 L4 pin wells | 2021-02-05 | 13:05 | 6.9 | 9.4 | 11.3 | 0 | 0 | 72.4 | 959 | -56.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR010305 | M1 L5 pin wells | 2021-01-08 | 13:54 | 74.7 | 31.4 | 1.1 | 26 | 7 | 0 | 971 | -5.31 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010307 | pin well line | 2021-01-08 | 13:56 | 50.7 | 25.7 | 6.4 | 17 | 28 | 17.2 | 972 | -0.21 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010308 | pin well line | 2021-01-08 | 14:02 | 47.6 | 29.5 | 6.3 | 19 | 19 | 16.6 | 970 | -2.1 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR01030A | M1 L3 pin well line A | 2021-01-08 | 13:44 | 12 | 9.8 | 9.5 | 20 | 15 | 68.7 | 972 | -1.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR010SR1 | M1 side riser 1 | 2021-03-03 | 13:16 | 53.9 | 34.6 | 0.1 | 3 | 4 | 11.4 | 980 | -38.89 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR010SR1 | M1 side riser 1 | 2021-03-03 | 13:16 | 53.4 | 34.4 | 0.1 | 1 | 10 | 12.1 | 980 | -40.37 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR010SR2 | M1 side riser 2 | 2021-03-03 | 13:15 | 58.2 | 38.5 | 0.7 | 9 | 0 | 2.6 | 979 | -197.79 |  | 50 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR020000 | Manifold 2 | 2021-01-04 | 14:34 | 44 | 34.2 | 2.6 | 38 | 30 | 19.2 | 972 | -157.69 |  | 100 | 0 | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR020000 | Manifold 2 | 2021-01-15 | 9:17 | 52.2 | 36 | 1.3 | 45 | 65 | 10.5 | 982 | -138.51 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR020000 | Manifold 2 | 2021-01-22 | 9:18 | 49.6 | 36.3 | 2 | 34 | 43 | 12.1 | 945 | -189.71 |  | 100 | 57 | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR020000 | Manifold 2 | 2021-01-25 | 15:41 | 45.5 | 35.5 | 1.9 | 26 | 68 | 17.1 | 965 | -169.9 |  | 100 | 59 | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR020000 | Manifold 2 | 2021-02-05 | 13:20 | 50.3 | 36 | 1.7 | 46 | 85 | 12 | 962 | -150.85 |  | 100 | 41 | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR020000 | Manifold 2 | 2021-02-08 | 14:30 | 45 | 35.1 | 3.4 | 25 | 74 | 16.5 | 958 | -199.82 |  | 100 | 47 | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR020000 | Manifold 2 | 2021-02-15 | 15:53 | 49.7 | 35.4 | 1.7 | 51 | 89 | 13.2 | 969 | -170.03 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR020000 | Manifold 2 | 2021-02-22 | 15:30 | 49.8 | 34.8 | 1.5 | 48 | 66 | 13.9 | 970 | -172.53 |  | 100 | 35 | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR020000 | Manifold 2 | 2021-03-03 | 13:36 | 43.7 | 32.8 | 2.3 | 33 | 37 | 21.2 | 982 | -188.01 |  | 100 | 26 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR020000 | Manifold 2 | 2021-03-09 | 9:48 | 45.5 | 32.9 | 2.3 | 40 | 5 | 19.3 | 974 | -211.75 |  | 100 | 80 | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR020000 | Manifold 2 | 2021-03-16 | 13:29 | 45.4 | 32.1 | 2 | 66 | 87 | 20.5 | 985 | -188.13 |  | 100 | 59 | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR020000 | Manifold 2 | 2021-03-25 | 13:59 | 49.9 | 34.4 | 1.8 | 57 | 84 | 13.9 | 972 | -182.16 |  | 100 | 70 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR020000 | Manifold 2 | 2021-03-30 | 13:57 | 48.1 | 32.9 | 1.7 | 78 | 75 | 17.3 | 982 | -176.66 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR020100 | MAN 2 LINE 1 | 2021-01-22 | 9:20 | 43.3 | 26.1 | 6 | 25 | 42 | 24.6 | 946 | -193.39 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR020100 | MAN 2 LINE 1 | 2021-02-08 | 14:31 | 54.4 | 32.8 | 1.1 | 17 | 75 | 11.7 | 957 | -203.64 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR020100 | MAN 2 LINE 1 | 2021-03-03 | 13:38 | 50.9 | 29.3 | 0.7 | 13 | 62 | 19.1 | 980 | -188.13 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR020200 | MAN 2 LINE 2 | 2021-01-22 | 9:22 | 49.9 | 36.2 | 2.3 | 46 | 83 | 11.6 | 946 | -193.98 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR020200 | MAN 2 LINE 2 | 2021-02-08 | 0.60694 | 44.5 | 34.3 | 3.4 | 30 | 93 | 17.8 | 957 | -202.64 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR020200 | MAN 2 LINE 2 | 2021-03-03 | 13:41 | 27.5 | 21.4 | 8.9 | 26 | 32 | 42.2 | 980 | -188.44 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030000 | Manifold 3 | 2021-01-04 | 14:39 | 45.6 | 35.4 | 0.8 | 31 | 29 | 18.2 | 973 | -157.25 |  | 100 | 251 | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR030000 | Manifold 3 | 2021-01-15 | 9:20 | 53.8 | 36.2 | 0.6 | 37 | 46 | 9.4 | 983 | -137.43 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR030000 | Manifold 3 | 2021-01-22 | 9:26 | 55.9 | 37.7 | 0.5 | 32 | 34 | 5.9 | 947 | -194.15 |  | 100 | 304 | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR030000 | Manifold 3 | 2021-01-25 | 15:46 | 46.7 | 36.7 | 0.3 | 19 | 40 | 16.3 | 967 | -174.09 |  | 100 | 245 | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR030000 | Manifold 3 | 2021-02-05 | 13:24 | 48.3 | 36 | 0.3 | 28 | 43 | 15.4 | 960 | -153.92 |  | 100 | 243 | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR030000 | Manifold 3 | 2021-02-08 | 14:38 | 48.1 | 36.6 | 0.6 | 22 | 41 | 14.7 | 957 | -204.01 |  | 100 | 227 | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR030000 | Manifold 3 | 2021-02-15 | 15:56 | 43.4 | 34.5 | 0.4 | 38 | 48 | 21.7 | 971 | -175.3 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR030000 | Manifold 3 | 2021-02-22 | 15:35 | 49.9 | 34.8 | 0.3 | 29 | 31 | 15 | 971 | -172.49 |  | 100 | 225 | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR030000 | Manifold 3 | 2021-03-03 | 13:45 | 46.2 | 34.5 | 0.5 | 13 | 15 | 18.8 | 982 | -187.68 |  | 100 | 188 | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030000 | Manifold 3 | 2021-03-09 | 9:52 | 46 | 34 | 0.6 | 30 | 9 | 19.4 | 969 | -209.25 |  | 100 | 305 | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR030000 | Manifold 3 | 2021-03-16 | 13:34 | 46.4 | 33.5 | 0.7 | 44 | 34 | 19.4 | 983 | -189.64 |  | 100 | 311 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR030000 | Manifold 3 | 2021-03-25 | 14:03 | 50.1 | 35.1 | 0.4 | 42 | 37 | 14.4 | 971 | -181.93 |  | 100 | 274 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR030000 | Manifold 3 | 2021-03-30 | 14:00 | 47.9 | 33.7 | 0.8 | 46 | 19 | 17.6 | 983 | -173.72 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR030100 | MAN 3 LINE 1 | 2021-01-22 | 9:27 | 55.8 | 38.4 | 0.3 | 30 | 48 | 5.5 | 946 | -193.39 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR030100 | MAN 3 LINE 1 | 2021-02-08 | 14:39 | 49.9 | 37.3 | 0.5 | 19 | 49 | 12.3 | 956 | -202.71 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR030100 | MAN 3 LINE 1 | 2021-03-03 | 13:46 | 47.3 | 35.1 | 0.3 | 19 | 31 | 17.3 | 979 | -186.86 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030101 | Man 3 line 1 line 1 | 2021-03-03 | 13:51 | 63.5 | 39.2 | 0.3 | 12 | 0 | 0 | 979 | -0.45 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030101 | Man 3 line 1 line 1 | 2021-03-03 | 13:52 | 62.1 | 38.3 | 0.6 | 16 | 0 | 0 | 979 | -1.91 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030101 | Man 3 line 1 line 1 | 2021-03-03 | 13:55 | 48.1 | 32.9 | 1.1 | 9 | 0 | 17.9 | 980 | -1.13 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0301LS | M1 L1 leachate sump | 2021-03-03 | 13:53 | 1 | 2.2 | 18.6 | 0 | 0 | 78.2 | 980 | -2.92 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030200 | MAN 3 LINE 2 | 2021-01-22 | 9:28 | 3.4 | 3.6 | 16.3 | 19 | 17 | 76.7 | 946 | -15.05 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR030200 | MAN 3 LINE 2 | 2021-02-08 | 14:40 | 8.2 | 11 | 13 | 11 | 23 | 67.8 | 957 | -13.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR030200 | MAN 3 LINE 2 | 2021-03-03 | 13:48 | 0 | 0.2 | 20.6 | 2 | 3 | 79.2 | 979 | -0.49 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030201 | M3 L2 w1 | 2021-03-03 | 13:50 | 28.7 | 13.3 | 6.3 | 0 | 0 | 51.7 | 981 | -2.57 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR030300 | MAN 3 LINE 3 | 2021-01-22 | 9:29 | 56.5 | 37.9 | 0.7 | 25 | 12 | 4.9 | 946 | -185.91 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR030300 | MAN 3 LINE 3 | 2021-02-08 | 14:41 | 48.1 | 36.7 | 0.9 | 15 | 9 | 14.3 | 957 | -203.99 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR030300 | MAN 3 LINE 3 | 2021-03-03 | 13:49 | 46.3 | 34.6 | 0.5 | 12 | 4 | 18.6 | 980 | -185.94 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR03A000 | Manifold 3A | 2021-01-04 | 14:45 | 46.4 | 34.2 | 2.4 | 28 | 20 | 17 | 973 | -155.81 |  | 100 | 151 | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR03A000 | Manifold 3A | 2021-01-15 | 9:23 | 55.4 | 37.6 | 0.9 | 35 | 29 | 6.1 | 982 | -138.44 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR03A000 | Manifold 3A | 2021-01-22 | 9:33 | 50.2 | 35.6 | 3.1 | 26 | 21 | 11.1 | 948 | -188.39 |  | 100 | 121 | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR03A000 | Manifold 3A | 2021-01-25 | 15:51 | 47.9 | 36.9 | 1.5 | 20 | 27 | 13.7 | 966 | -169.66 |  | 100 | 143 | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR03A000 | Manifold 3A | 2021-02-05 | 13:28 | 50.8 | 35.4 | 2.7 | 31 | 25 | 11.1 | 959 | -147.88 |  | 100 | 92 | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR03A000 | Manifold 3A | 2021-02-08 | 14:45 | 54.5 | 38.4 | 1.4 | 22 | 26 | 5.7 | 957 | -202.67 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR03A000 | Manifold 3A | 2021-02-15 | 16:00 | 49.7 | 35 | 2.3 | 36 | 37 | 13 | 970 | -173.18 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR03A000 | Manifold 3A | 2021-02-22 | 15:40 | 48.5 | 34.6 | 3 | 31 | 22 | 13.9 | 973 | -172.77 |  | 100 | 116 | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR03A000 | Manifold 3A | 2021-03-03 | 14:00 | 37.1 | 31.1 | 2.1 | 15 | 9 | 29.7 | 980 | -184.38 |  | 100 | 80 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR03A000 | Manifold 3A | 2021-03-09 | 9:58 | 44.5 | 31.1 | 5.4 | 48 | 6 | 19 | 974 | -203.09 |  | 100 | 70 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR03A000 | Manifold 3A | 2021-03-16 | 13:42 | 55.8 | 37.7 | 1.6 | 60 | 48 | 4.9 | 983 | -187.29 |  | 100 | 74 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR03A000 | Manifold 3A | 2021-03-25 | 14:09 | 55.8 | 38.6 | 1.6 | 53 | 69 | 4 | 970 | -182.7 |  | 100 | 65 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR03A000 | Manifold 3A | 2021-03-30 | 14:04 | 52.4 | 36.1 | 1.3 | 64 | 29 | 10.2 | 981 | -173.01 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR03A200 | manifold 3A line 2 | 2021-01-22 | 9:35 | 53.1 | 37.3 | 1.5 | 34 | 14 | 8.1 | 944 | -189.39 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR03A200 | manifold 3A line 2 | 2021-02-08 | 14:46 | 54.2 | 38 | 1.9 | 26 | 13 | 5.9 | 955 | -202.86 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR03A200 | manifold 3A line 2 | 2021-03-03 | 14:01 | 36.5 | 31.2 | 1.9 | 19 | 2 | 30.4 | 977 | -182.61 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR03A300 | M3 L3 | 2021-01-22 | 9:36 | 40.4 | 26.3 | 6.7 | 26 | 9 | 26.6 | 944 | -191.04 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR03A300 | M3 L3 | 2021-02-08 | 14:47 | 47.4 | 31.1 | 0.7 | 21 | 17 | 20.8 | 955 | -204.04 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR03A300 | M3 L3 | 2021-02-15 | 16:01 | 41.2 | 28.8 | 3.9 | 29 | 22 | 26.1 | 968 | -173.97 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR03A300 | M3 L3 | 2021-03-03 | 14:02 | 42.2 | 28.7 | 4.4 | 12 | 2 | 24.7 | 977 | -182.07 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR040000 | Manifold 4 | 2021-01-15 | 10:43 | 0.5 | 0.3 | 19 | 17 | 2 | 80.2 | 980 | -0.52 |  | 0 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR040000 | Manifold 4 | 2021-01-18 | 14:47 | 41.7 | 28.8 | 7.3 | 30 | 47 | 22.2 | 972 | -134.1 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR040000 | Manifold 4 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR040000 | Manifold 4 | 2021-02-01 | 14:39 | 0.3 | 0.8 | 19.6 | 8 | 6 | 79.3 | 951 | -92 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040000 | Manifold 4 | 2021-02-08 | 13:31 | 35.7 | 27.1 | 5.7 | 13 | 131 | 31.5 | 955 | -189.52 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR040000 | Manifold 4 | 2021-02-15 | 14:54 | 36.3 | 27.4 | 3.7 | 29 | 100 | 32.6 | 968 | -162.25 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR040000 | Manifold 4 | 2021-02-22 | 14:41 | 39.2 | 30.5 | 4.3 | 18 | 33 | 26 | 968 | -157.95 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR040000 | Manifold 4 | 2021-03-02 | 14:28 | 36.3 | 28.4 | 3.8 | 18 | 35 | 31.5 | 982 | -187.17 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR040000 | Manifold 4 | 2021-03-08 | 14:28 | 53.9 | 36.5 | 2 | 40 | 36 | 7.6 | 977 | -199.39 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR040000 | Manifold 4 | 2021-03-16 | 12:42 | 51.3 | 35 | 1.8 | 34 | 24 | 11.9 | 984 | -184.15 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR040000 | Manifold 4 | 2021-03-25 | 13:05 | 55.6 | 38.8 | 1.2 | 41 | 37 | 4.4 | 970 | -173.2 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR040000 | Manifold 4 | 2021-03-30 | 13:12 | 54.5 | 36 | 1 | 43 | 50 | 8.5 | 981 | -170.18 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR040100 | M4 L1 | 2021-01-18 | 14:47 | 11.1 | 6.1 | 15.8 | 27 | 33 | 67 | 969 | -131.69 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR040100 | M4 L1 | 2021-02-08 | 13:32 | 17.5 | 12.9 | 14.8 | 10 | 24 | 54.8 | 955 | -189.71 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR040100 | M4 L1 | 2021-03-08 | 14:29 | 4 | 3.2 | 19.3 | 26 | 10 | 73.5 | 975 | -200.33 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR040101 | M4 L1 pin 1 | 2021-01-29 | 14:18 | 52 | 32.6 | 1.9 | 7 | 130 | 13.5 | 953 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040102 | M4 L1 PIN2 | 2021-01-29 | 14:19 | 40.5 | 27.1 | 5 | 11 | 50 | 27.4 | 954 | -0.35 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040103 | M4 L1 pin 3 | 2021-01-29 | 14:20 | 48.2 | 33.2 | 3.7 | 11 | 58 | 14.9 | 954 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040104 | M4 L1 pin 4 | 2021-01-29 | 14:21 | 1 | 1.3 | 13.6 | 0 | 22 | 84.1 | 954 | -0.57 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040105 | M4 L1 pin 5 | 2021-01-29 | 14:21 | 0.1 | 0.2 | 21.3 | 0 | 5 | 78.4 | 955 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040106 | M4 L1 pin 6 | 2021-01-29 | 14:22 | 46.2 | 32.1 | 2.2 | 3 | 60 | 19.5 | 954 | -0.45 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040107 | M4 L1 pin 7 | 2021-01-29 | 14:23 | 25.2 | 22.3 | 5.2 | 6 | 36 | 47.3 | 955 | -0.54 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040108 | M4 L1 pin 8 | 2021-01-29 | 14:25 | 38.3 | 27.4 | 4.3 | 6 | 49 | 30 | 954 | -0.19 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040200 | MAN 4 LINE 2 | 2021-01-18 | 14:48 | 44.1 | 29.8 | 6.2 | 33 | 43 | 19.9 | 969 | -136.67 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR040200 | MAN 4 LINE 2 | 2021-02-08 | 13:33 | 34.3 | 25.9 | 6.7 | 16 | 40 | 33.1 | 955 | -181.17 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR040200 | MAN 4 LINE 2 | 2021-03-08 | 14:30 | 54.8 | 36.8 | 1.2 | 50 | 7 | 7.2 | 975 | -200.81 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR040201 | M4 L1 pw 1 | 2021-01-29 | 14:29 | 40.3 | 21.9 | 7.1 | 12 | 10 | 30.7 | 954 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040202 | M4 L2 pw 2 | 2021-01-29 | 14:28 | 51.6 | 27.1 | 2.6 | 17 | 19 | 18.7 | 954 | -0.31 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040203 | M4 L2 pw 3 | 2021-01-29 | 14:26 | 40.7 | 30.9 | 4.1 | 8 | 71 | 24.3 | 954 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040300 | MAN 4 L3 | 2021-01-18 | 14:49 | 26.9 | 15.9 | 12 | 32 | 29 | 45.2 | 969 | -132.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR040300 | MAN 4 L3 | 2021-02-08 | 13:34 | 33.6 | 26 | 5.9 | 21 | 25 | 34.5 | 955 | -190.47 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR040300 | MAN 4 L3 | 2021-03-08 | 14:31 | 49.7 | 34 | 2.7 | 54 | 9 | 13.6 | 975 | -200.97 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR040301 | MAN 4 L3 PW1 | 2021-01-29 | 14:40 | 58.3 | 29.3 | 1.3 | 18 | 9 | 11.1 | 954 | 0.05 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040302 | MAN 4 L3 PW2 | 2021-01-29 | 14:38 | 69.3 | 30.3 | 0.7 | 16 | 15 | 0 | 953 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040302 | MAN 4 L3 PW2 | 2021-01-29 | 14:39 | 65.3 | 31.7 | 0.2 | 18 | 13 | 2.8 | 953 | -3.97 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040303 | MAN 4 L3 PW3 | 2021-01-29 | 14:36 | 67.3 | 30.6 | 0.5 | 16 | 36 | 1.6 | 954 | -0.05 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040303 | MAN 4 L3 PW3 | 2021-01-29 | 14:37 | 57.2 | 30.4 | 0 | 13 | 26 | 12.4 | 954 | -2.5 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040303 | MAN 4 L3 PW3 | 2021-01-29 | 14:37 | 55.6 | 29.7 | 0 | 12 | 21 | 14.7 | 954 | -1.13 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040304 | MAN 4 L3 PW4 | 2021-01-29 | 14:34 | 64.6 | 33.3 | 0.4 | 14 | 22 | 1.7 | 954 | -0.02 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040304 | MAN 4 L3 PW4 | 2021-01-29 | 14:35 | 65.4 | 33.8 | 0 | 17 | 29 | 0.8 | 954 | -1.61 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040305 | MAN 4 L3 PW5 | 2021-01-29 | 14:33 | 58.2 | 31.6 | 0.4 | 12 | 18 | 9.8 | 953 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040305 | MAN 4 L3 PW5 | 2021-01-29 | 14:44 | 53.6 | 31.2 | 0.6 | 10 | 3 | 14.6 | 954 | -1.13 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR040305 | MAN 4 L3 PW5 | 2021-01-29 | 14:44 | 52.2 | 30.5 | 0.3 | 10 | 2 | 17 | 954 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-01-15 | 10:39 | 22.1 | 11.5 | 15.5 | 20 | 33 | 50.9 | 980 | -148.77 |  | 100 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR050000 | Manifold 5 | 2021-01-15 | 10:39 | 22 | 11.6 | 15 | 18 | 37 | 51.4 | 980 | -143.72 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR050000 | Manifold 5 | 2021-01-22 | 10:44 | 26.8 | 16.3 | 12.5 | 11 | 111 | 44.4 | 945 | -80.32 |  | 0 | 0 | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-01-27 | 10:13 | 64.4 | 33.6 | 1.5 | 0 | 151 | 0.5 | 964 | -122.13 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR050000 | Manifold 5 | 2021-01-27 | 10:14 | 63.7 | 33.2 | 1.4 | 0 | 187 | 1.7 | 964 | -145.57 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR050000 | Manifold 5 | 2021-01-29 | 13:16 | 58.8 | 34.8 | 0.9 | 24 | 380 | 5.5 | 955 | -147.24 |  | 100 |  | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-02-03 | 13:05 | 45.3 | 31.8 | 0.2 | 40 | 368 | 22.7 | 948 | -134.67 |  | 100 | 0 | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR050000 | Manifold 5 | 2021-02-16 | 10:37 | 56.2 | 33.1 | 1.1 | 6 | 150 | 9.6 | 959 | -189.97 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-02-26 | 13:34 | 55.7 | 32.8 | 0.8 | 14 | 178 | 10.7 | 988 | -159.3 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-03-05 | 12:58 | 48.9 | 30.4 | 0.6 | 5 | 29 | 20.1 | 984 | -187.61 |  | 100 | 0 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR050000 | Manifold 5 | 2021-03-09 | 11:40 | 68.5 | 33.3 | 0.8 | 21 | 328 | 0 | 971 | -202.72 |  | 100 | 0 | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR050000 | Manifold 5 | 2021-03-16 | 14:35 | 51.2 | 29.7 | 1.1 | 37 | 156 | 18 | 983 | -191.13 |  | 100 | 68 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR050000 | Manifold 5 | 2021-03-25 | 13:16 | 64.2 | 34.2 | 0.7 | 26 | 120 | 0.9 | 969 | -179.17 |  | 100 | 0 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR050000 | Manifold 5 | 2021-03-30 | 13:21 | 62.2 | 33.5 | 0.9 | 37 | 65 | 3.4 | 980 | -181.05 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR050100 | MAN 5 LINE 1 | 2021-01-22 | 10:47 | 0 | 0.2 | 20.2 | 6 | 51 | 79.6 | 945 | -0.21 |  | 0 |  | sample/flow point inaccessible |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR050100 | MAN 5 LINE 1 | 2021-01-29 | 13:19 | 56.9 | 31.7 | 0.7 | 11 | 132 | 10.7 | 953 | -95.49 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050100 | MAN 5 LINE 1 | 2021-02-16 | 14:58 | 47.2 | 29.5 | 2.1 | 0 | 70 | 21.2 | 957 | -173.34 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR050100 | MAN 5 LINE 1 | 2021-03-05 | 12:59 | 34.2 | 26 | 2 | 0 | 18 | 37.8 | 983 | -186.18 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR050104 | M5 L1 PW L4 | 2021-03-30 | 15:00 | 27.3 | 22.9 | 0.2 | 25 | 10 | 49.6 | 978 | -85.18 |  | 10 |  | Investigation/attention required |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR050104 | M5 L1 PW L4 | 2021-03-30 | 15:00 | 27 | 23.1 | 0.3 | 25 | 10 | 49.6 | 978 | 0.17 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR050105 | M5 L1 PW L5 | 2021-01-29 | 13:31 | 55.9 | 30.3 | 3.1 | 18 | 884 | 10.7 | 955 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050106 | M5 L1 PW L6 | 2021-01-29 | 13:33 | 59.5 | 32.5 | 0.4 | 13 | 227 | 7.6 | 953 | -0.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050106 | M5 L1 PW L6 | 2021-01-29 | 13:34 | 56.8 | 32 | 0.1 | 13 | 81 | 11.1 | 953 | -0.8 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050106 | M5 L1 PW L6 | 2021-03-30 | 14:58 | 27.2 | 23 | 0.4 | 25 | 9 | 49.4 | 979 | -0.85 |  | 10 |  | Investigation/attention required |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR050106 | M5 L1 PW L6 | 2021-03-30 | 14:59 | 26.5 | 22.9 | 0.3 | 25 | 9 | 50.3 | 979 | -0.33 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR050107 | M5 L1 PW L7 | 2021-01-29 | 13:35 | 57 | 30.1 | 0.4 | 11 | 68 | 12.5 | 954 | -0.35 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050107 | M5 L1 PW L7 | 2021-01-29 | 13:36 | 53.9 | 30 | 0.4 | 11 | 50 | 15.7 | 954 | -0.82 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050107 | M5 L1 PW L7 | 2021-01-29 | 13:36 | 52.8 | 29.7 | 0.4 | 10 | 46 | 17.1 | 954 | -0.28 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-01-18 | 14:53 | 50.9 | 35.3 | 0.9 | 84 | 732 | 12.9 | 971 | -135.19 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-02-03 | 13:10 | 36.8 | 31.1 | 0.6 | 53 | 783 | 31.5 | 950 | -133.98 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-02-03 | 13:20 | 44.4 | 34.2 | 0.7 | 59 | 1030 | 20.7 | 950 | -136.34 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-02-15 | 14:46 | 35.7 | 29.2 | 1.4 | 61 | 399 | 33.7 | 969 | -158.81 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-02-15 | 14:52 | 35.4 | 29.3 | 1.1 | 63 | 379 | 34.2 | 971 | -163.29 |  | 100 |  | Investigation/attention required |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A0 | M5 L1A | 2021-03-08 | 14:37 | 52.5 | 21.2 | 0.8 | 30 | 25 | 25.5 | 977 | -205.22 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR0501A1 | M5 L1A PW1 | 2021-01-07 | 15:46 | 45.7 | 36.4 | 0.5 | 24 | 7 | 17.4 | 968 | -0.68 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0501A1 | M5 L1A PW1 | 2021-01-15 | 10:52 | 52.8 | 35.5 | 0.6 | 86 | 1327 | 11.1 | 980 | -0.05 |  | 10 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR0501A1 | M5 L1A PW1 | 2021-01-29 | 13:23 | 45.2 | 33.8 | 1.2 | 55 | 1064 | 19.8 | 953 | -0.02 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-03 | 13:15 | 42 | 32.8 | 0.5 | 59 | 1177 | 24.7 | 948 | -2.53 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-15 | 14:48 | 38.9 | 29.8 | 2.4 | 57 | 706 | 28.9 | 968 | -1.18 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-15 | 14:48 | 38.2 | 29.2 | 2.3 | 57 | 744 | 30.3 | 968 | -0.35 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-26 | 14:33 | 55.9 | 36.4 | 0.6 | 53 | 15 | 7.1 | 988 | -5.48 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-26 | 14:34 | 57.9 | 40.3 | 0.3 | 52 | 8 | 1.5 | 988 | -2.41 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-02-26 | 14:43 | 60 | 35.8 | 0.8 | 71 | 11 | 3.4 | 989 | -0.5 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-03-19 | 14:27 | 20.9 | 19.8 | 4.2 | 9 | 1 | 55.1 | 981 | -0.56 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A1 | M5 L1A PW1 | 2021-03-19 | 14:28 | 21.2 | 21.1 | 4 | 9 | 2 | 53.7 | 981 | -0.62 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-01-07 | 15:47 | 40.3 | 35.1 | 0.2 | 30 | 7 | 24.4 | 968 | -0.69 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0501A2 | M5 L1A PW2 | 2021-01-15 | 10:53 | 52.5 | 35.7 | 0.3 | 74 | 634 | 11.5 | 981 | -2.5 |  | 10 |  | Gas depletes when adjusted |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR0501A2 | M5 L1A PW2 | 2021-01-29 | 13:24 | 48.6 | 34.9 | 0.7 | 54 | 495 | 15.8 | 954 | -0.94 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-03 | 13:16 | 42.3 | 32.8 | 0.8 | 45 | 264 | 24.1 | 949 | -8.07 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-15 | 14:49 | 33.3 | 28.3 | 1 | 63 | 294 | 37.4 | 968 | -8.14 |  | 30 |  | Investigation/attention required |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-15 | 14:49 | 32.2 | 27.7 | 0.9 | 59 | 211 | 39.2 | 968 | 0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-26 | 14:35 | 26.7 | 26.3 | 2.3 | 55 | 7 | 44.7 | 988 | -1.86 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-26 | 14:36 | 51.9 | 38.9 | 0.1 | 66 | 8 | 9.1 | 988 | -0.3 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-02-26 | 14:45 | 52.7 | 37.3 | 0.6 | 78 | 11 | 9.4 | 989 | -0.02 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-03-19 | 14:29 | 24.6 | 24.9 | 3.1 | 12 | 4 | 47.4 | 981 | -4.95 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A2 | M5 L1A PW2 | 2021-03-19 | 14:29 | 24.5 | 25.4 | 2.7 | 11 | 5 | 47.4 | 981 | -0.78 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-01-07 | 15:49 | 55 | 41.1 | 0.1 | 36 | 9 | 3.8 | 968 | -1.61 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0501A3 | M5 L1A PW3 | 2021-01-07 | 15:50 | 51.3 | 39.5 | 0.2 | 35 | 11 | 9 | 968 | -4.48 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0501A3 | M5 L1A PW3 | 2021-01-15 | 10:54 | 46.8 | 34.9 | 0.2 | 84 | 703 | 18.1 | 981 | -1.11 |  | 20 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR0501A3 | M5 L1A PW3 | 2021-01-29 | 13:25 | 44.9 | 35.4 | 0.2 | 86 | 903 | 19.5 | 954 | -0.17 |  | 20 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-02-03 | 13:17 | 39.5 | 32.8 | 0.3 | 63 | 826 | 27.4 | 948 | -2.05 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-02-03 | 13:18 | 50.6 | 37.5 | 0.1 | 81 | 1593 | 11.8 | 948 | -0.12 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-02-15 | 14:50 | 52.7 | 38 | 0.1 | 84 | 1438 | 9.2 | 967 | -0.47 |  | 10 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-02-26 | 14:37 | 50.2 | 39.5 | 0.2 | 76 | 12 | 10.1 | 989 | -1.13 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-03-19 | 14:30 | 36.9 | 32.2 | 0.7 | 14 | 7 | 30.2 | 981 | -0.94 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A3 | M5 L1A PW3 | 2021-03-19 | 14:30 | 36.7 | 31.5 | 0.9 | 14 | 7 | 30.9 | 981 | -1.48 |  | 10 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-01-29 | 13:26 | 63.1 | 40.7 | 2.7 | 90 | 5397 | 0 | 955 | -0.14 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-01-29 | 13:28 | 59.3 | 41.5 | 0.2 | 88 | 625 | 0 | 955 | -10.95 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-02-03 | 13:14 | 33 | 28.9 | 0.8 | 52 | 740 | 37.3 | 948 | -15.64 |  | 20 |  | Investigation/attention required |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-02-03 | 13:14 | 32.2 | 28.5 | 0.2 | 54 | 811 | 39.1 | 948 | -0.36 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-02-26 | 14:38 | 59 | 39.7 | 0 | 78 | 19 | 1.3 | 989 | -1.3 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-02-26 | 14:38 | 37.9 | 30.2 | 1.1 | 60 | 6 | 30.8 | 989 | -0.14 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-02-26 | 14:46 | 60.5 | 36.4 | 0.7 | 86 | 151 | 2.4 | 990 | -0.92 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-03-19 | 14:31 | 18.3 | 25.4 | 2.8 | 12 | 6 | 53.5 | 981 | -101.82 |  | 60 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A4 | MAN 5 L1 A4 | 2021-03-19 | 14:31 | 17.2 | 24.5 | 2.9 | 11 | 5 | 55.4 | 981 | -1.15 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-02-26 | 14:25 | 2.2 | 7.1 | 18.7 | 9 | 20 | 72 | 988 | -0.16 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-02-26 | 14:26 | 51.6 | 32.5 | 1.6 | 62 | 13 | 14.3 | 988 | -1.34 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-02-26 | 14:27 | 46.4 | 31.6 | 2.7 | 62 | 21 | 19.3 | 988 | -1.65 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-02-26 | 14:40 | 39.5 | 29 | 4.8 | 83 | 17 | 26.7 | 989 | -0.12 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-02-26 | 14:40 | 39 | 27.9 | 5 | 78 | 15 | 28.1 | 989 | 0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A5 | M5 L1A PIN LINE 5 | 2021-03-19 | 14:32 | 32.8 | 23.5 | 6.6 | 25 | 7 | 37.1 | 981 | -0.57 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A6 | M5 L1A PIN LINE 6 | 2021-02-26 | 14:28 | 26.6 | 20.8 | 10.9 | 39 | 16 | 41.7 | 988 | -0.62 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A6 | M5 L1A PIN LINE 6 | 2021-02-26 | 14:29 | 57.7 | 36.1 | 0.3 | 58 | 13 | 5.9 | 988 | -0.75 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A6 | M5 L1A PIN LINE 6 | 2021-02-26 | 14:41 | 48.7 | 36.7 | 1.1 | 88 | 20 | 13.5 | 988 | -0.64 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A6 | M5 L1A PIN LINE 6 | 2021-03-19 | 14:33 | 34.7 | 26 | 2.7 | 19 | 10 | 36.6 | 982 | -2.5 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A6 | M5 L1A PIN LINE 6 | 2021-03-19 | 14:33 | 33.8 | 26 | 2.7 | 18 | 9 | 37.5 | 982 | -1.8 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR0501A7 | M5 L1A PIN LINE 7 | 2021-02-26 | 14:30 | 5.3 | 17.9 | 12.2 | 51 | 11 | 64.6 | 988 | -0.64 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A7 | M5 L1A PIN LINE 7 | 2021-02-26 | 14:31 | 34.3 | 31.4 | 0.3 | 47 | 17 | 34 | 988 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A7 | M5 L1A PIN LINE 7 | 2021-02-26 | 14:31 | 30.9 | 27.3 | 0.9 | 59 | 10 | 40.9 | 988 | -0.43 |  | 10 |  | Investigation/attention required |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0501A7 | M5 L1A PIN LINE 7 | 2021-03-19 | 14:35 | 35.3 | 27.6 | 3.2 | 33 | 14 | 33.9 | 981 | -0.75 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR050200 | MAN 5 LINE 2 | 2021-01-22 | 10:46 | 49.5 | 28.1 | 4.9 | 11 | 207 | 17.5 | 944 | -68.24 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR050200 | MAN 5 LINE 2 | 2021-02-03 | 13:06 | 60 | 34.1 | 0.5 | 23 | 349 | 5.4 | 947 | -133.7 |  | 100 |  | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050200 | MAN 5 LINE 2 | 2021-03-05 | 13:00 | 63.7 | 32.2 | 0.6 | 0 | 225 | 3.5 | 983 | -187.07 |  | 100 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR050400 | MANIFOLD 6 LINE 4 | 2021-01-22 | 10:48 | 0 | 0.3 | 20.7 | 5 | 18 | 79 | 945 | 0 |  | 0 |  | sample/flow point inaccessible |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR050400 | MANIFOLD 6 LINE 4 | 2021-01-29 | 13:17 | 54.5 | 32.1 | 2.1 | 26 | 410 | 11.3 | 953 | -151.07 |  | 100 |  | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050400 | MANIFOLD 6 LINE 4 | 2021-02-03 | 13:07 | 46 | 29.3 | 2.4 | 27 | 367 | 22.3 | 948 | -132.37 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR050400 | MANIFOLD 6 LINE 4 | 2021-03-05 | 13:01 | 41.5 | 24.2 | 4.9 | 0 | 61 | 29.4 | 983 | -187.68 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR050400 | MANIFOLD 6 LINE 4 | 2021-03-05 | 13:02 | 40.5 | 23.9 | 4.9 | 0 | 37 | 30.7 | 983 | -187.33 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060000 | Manifold 6 | 2021-01-15 | 11:05 | 47.9 | 33.6 | 0.9 | 29 | 37 | 17.6 | 982 | -161.38 |  | 100 |  | Condition good |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR060000 | Manifold 6 | 2021-01-18 | 14:23 | 45.4 | 32.3 | 1 | 30 | 2 | 21.3 | 971 | -134.74 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR060000 | Manifold 6 | 2021-01-29 | 15:14 | 42.7 | 32.9 | 1.8 | 27 | 41 | 22.6 | 954 | -133.67 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-02-01 | 14:14 | 50.1 | 35.4 | 0.9 | 18 | 0 | 13.6 | 952 | -156.32 |  | 100 | 423 | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-02-11 | [13 empty] | 23 | Sample point frozen | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR060000 | Manifold 6 | 2021-02-15 | 14:22 | 45.1 | 33.1 | 0.9 | 29 | 12 | 20.9 | 970 | -164.02 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-02-22 | 14:19 | 42.6 | 32.7 | 0.7 | 14 | 0 | 24 | 969 | -167.6 |  | 100 | 0 | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-03-02 | 13:57 | 37.8 | 30.3 | 1 | 13 | 0 | 30.9 | 981 | -199.58 |  | 100 | 425 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060000 | Manifold 6 | 2021-03-08 | 13:59 | 45.4 | 33.6 | 0.9 | 34 | 1 | 20.1 | 976 | -204.11 |  | 100 | 215 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR060000 | Manifold 6 | 2021-03-15 | 14:36 | 33 | 27.1 | 2 | 24 | 2 | 37.9 | 977 | -177.85 |  | 100 | 182 | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR060000 | Manifold 6 | 2021-03-15 | 15:14 | 48.2 | 35.1 | 1.1 | 35 | 47 | 15.6 | 978 | -193.56 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR060000 | Manifold 6 | 2021-03-25 | 12:42 | 55.7 | 37.7 | 0.8 | 31 | 5 | 5.8 | 967 | -176.01 |  | 100 | 208 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR060000 | Manifold 6 | 2021-03-30 | 12:49 | 51.9 | 36.2 | 0.6 | 29 | 3 | 11.3 | 982 | -184.99 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR060100 | MAN 6 LINE 1 | 2021-01-18 | 14:25 | 54.5 | 37.3 | 0.5 | 28 | 8 | 7.7 | 971 | -134.52 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR060100 | MAN 6 LINE 1 | 2021-01-29 | 15:15 | 48.6 | 35 | 2 | 23 | 46 | 14.4 | 955 | -134.54 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060100 | MAN 6 LINE 1 | 2021-02-15 | 14:23 | 48.1 | 34.2 | 0.2 | 28 | 26 | 17.5 | 969 | -164.58 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR060100 | MAN 6 LINE 1 | 2021-03-02 | 13:59 | 49.9 | 35.7 | 0.4 | 17 | 0 | 14 | 981 | -199.27 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060100 | MAN 6 LINE 1 | 2021-03-15 | 14:38 | 49 | 34.5 | 1.2 | 30 | 8 | 15.3 | 977 | -178.89 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR060101 | M6 L1 pin well line 1 | 2021-02-01 | 14:16 | 55.6 | 41.3 | 0.5 | 12 | 32 | 2.6 | 952 | -2.79 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060102 | M6 L1 pin well line 2 | 2021-02-01 | 14:17 | 39.4 | 33.8 | 0.4 | 3 | 20 | 26.4 | 952 | -3.45 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060102 | M6 L1 pin well line 2 | 2021-02-01 | 14:17 | 38.3 | 33.2 | 0.4 | 2 | 15 | 28.1 | 952 | -1.44 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060200 | MAN 6 LINE 2 | 2021-01-18 | 14:26 | 44.6 | 32 | 1.1 | 36 | 9 | 22.3 | 971 | -134.99 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR060200 | MAN 6 LINE 2 | 2021-01-29 | 15:16 | 41.4 | 32.2 | 2 | 26 | 33 | 24.4 | 955 | -135.25 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060200 | MAN 6 LINE 2 | 2021-02-15 | 14:24 | 45 | 32.9 | 0.9 | 33 | 24 | 21.2 | 970 | -166.17 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR060200 | MAN 6 LINE 2 | 2021-03-02 | 14:00 | 36.9 | 29.9 | 1 | 19 | 0 | 32.2 | 981 | -200.12 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060200 | MAN 6 LINE 2 | 2021-03-15 | 14:40 | 31.5 | 26.6 | 1.9 | 30 | 9 | 40 | 978 | -182.11 |  | 100 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR060200 | MAN 6 LINE 2 | 2021-03-15 | 15:13 | 45.6 | 34.9 | 0.9 | 33 | 24 | 18.6 | 979 | -197.98 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR060201 | M6 L2 Pin well line 1 | 2021-01-29 | 15:10 | 62.3 | 44.4 | 0 | 26 | 76 | 0 | 954 | -18.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060201 | M6 L2 Pin well line 1 | 2021-01-29 | 15:11 | 62.7 | 44.1 | 0 | 27 | 84 | 0 | 954 | -0.94 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060201 | M6 L2 Pin well line 1 | 2021-03-02 | 14:11 | 52.3 | 38.5 | 0.6 | 21 | 32 | 8.6 | 980 | -4.25 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060202 | M6 L2 pin well line 2 | 2021-01-29 | 15:09 | 39.9 | 29.7 | 0.1 | 20 | 38 | 30.3 | 955 | -0.38 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060203 | M6 L2 PL3 | 2021-01-29 | 15:08 | 48.3 | 33.7 | 0.4 | 32 | 24 | 17.6 | 954 | -7.12 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR060203 | M6 L2 PL3 | 2021-03-02 | 14:09 | 28 | 25.5 | 1.6 | 15 | 0 | 44.9 | 980 | -68.33 |  | 30 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR060203 | M6 L2 PL3 | 2021-03-02 | 14:10 | 26.9 | 24.8 | 1.6 | 16 | 0 | 46.7 | 981 | 0.05 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR070000 | Manifold 7 | 2021-01-08 | 15:00 | 62.5 | 36.5 | 1.8 | 49 | 186 | 0 | 970 | -101.49 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR070000 | Manifold 7 | 2021-01-15 | [13 empty] | 6 | No safe access | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR070000 | Manifold 7 | 2021-01-18 | 14:41 | 67.5 | 37.8 | 0.9 | 44 | 437 | 0 | 970 | -135.06 |  | 100 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR070000 | Manifold 7 | 2021-01-27 | [13 empty] | 6 | No safe access | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR070000 | Manifold 7 | 2021-02-01 | 14:33 | 62 | 37.6 | 1.3 | 30 | 456 | 0 | 951 | -124.09 |  | 100 | 22 | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR070000 | Manifold 7 | 2021-02-08 | 13:18 | 55.7 | 34.9 | 2.5 | 29 | 186 | 6.9 | 956 | -192.21 |  | 100 | 219 | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR070000 | Manifold 7 | 2021-02-15 | 14:42 | 60.9 | 37.8 | 0.3 | 45 | 252 | 1 | 969 | -144.08 |  | 100 |  | Condition good |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR070000 | Manifold 7 | 2021-02-22 | 14:36 | 59.3 | 37.1 | 0.2 | 35 | 415 | 3.4 | 969 | -169.68 |  | 100 | 2 | Condition good |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070000 | Manifold 7 | 2021-03-02 | 14:21 | 57.6 | 36.3 | 0.8 | 32 | 234 | 5.3 | 981 | -202.36 |  | 100 | 20 | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR070000 | Manifold 7 | 2021-03-08 | 14:21 | 60.2 | 36.5 | 0.7 | 45 | 268 | 2.6 | 978 | -201.59 |  | 100 | 157 | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR070000 | Manifold 7 | 2021-03-16 | 12:35 | 58.1 | 35.8 | 0.7 | 49 | 195 | 5.4 | 982 | -182.7 |  | 100 | 0 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR070000 | Manifold 7 | 2021-03-25 | 13:00 | 58.2 | 36 | 1 | 39 | 231 | 4.8 | 970 | -175.02 |  | 100 | 153 | Condition good |  |  | No | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR070000 | Manifold 7 | 2021-03-30 | 13:08 | 60.4 | 36.4 | 0.6 | 43 | 246 | 2.6 | 983 | -180.79 |  | 100 |  | Condition good |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR070300 | MAN 7 LINE 3 | 2021-01-08 | 15:01 | 62.1 | 36.2 | 1.5 | 46 | 362 | 0.2 | 969 | -100 |  | 100 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR070300 | MAN 7 LINE 3 | 2021-01-18 | 14:43 | 67.8 | 37.8 | 0.9 | 46 | 570 | 0 | 970 | -133.2 |  | 100 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR070300 | MAN 7 LINE 3 | 2021-02-08 | 13:19 | 55.8 | 34.9 | 2.4 | 30 | 365 | 6.9 | 956 | -194.36 |  | 100 |  | Condition good |  |  | No | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR070300 | MAN 7 LINE 3 | 2021-03-02 | 14:22 | 57.7 | 36.3 | 0.8 | 33 | 431 | 5.2 | 980 | -203.92 |  | 100 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR070301 | MAN 7 LINE 3 PIN LINE 1 | 2021-02-16 | 15:10 | 20.9 | 16.3 | 10.9 | 1 | 20 | 51.9 | 958 | -0.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070302 | MAN 7 LINE 3 PIN LINE 2 | 2021-02-16 | 15:09 | 36.7 | 31 | 0.6 | 9 | 49 | 31.7 | 959 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070303 | MAN 7 LINE 3 PIN LINE 3 | 2021-02-16 | 15:08 | 60.6 | 35.6 | 0.2 | 11 | 323 | 3.6 | 959 | -4.65 |  | 30 |  | Condition good |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070304 | MAN 7 LINE 3 PIN LINE 4 | 2021-02-16 | 15:07 | 46.9 | 22.5 | 0.4 | 0 | 7 | 30.2 | 958 | -2.52 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070305 | PIN WELLS | 2021-02-16 | 15:05 | 76.2 | 28.3 | 0.5 | 0 | 49 | 0 | 957 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR070305 | PIN WELLS | 2021-02-16 | 15:06 | 76.3 | 28.5 | 0.2 | 0 | 53 | 0 | 957 | -122.92 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-01-04 | 14:01 | 47 | 34.9 | 2 | 57 | 48 | 16.1 | 972 | -157.81 |  | 100 | 321 | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR080000 | Manifold 8 | 2021-01-15 | 8:46 | 30 | 26.2 | 3.7 | 58 | 64 | 40.1 | 982 | -112.25 |  | 100 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR080000 | Manifold 8 | 2021-01-15 | 8:54 | 54.7 | 37.9 | 1 | 55 | 94 | 6.4 | 981 | -127 |  | 100 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR080000 | Manifold 8 | 2021-01-18 | 15:07 | 56 | 38.2 | 0.6 | 65 | 80 | 5.2 | 971 | -137.12 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 70% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-01-25 | 14:42 | 56.9 | 39.7 | 0.4 | 66 | 97 | 3 | 965 | -127.82 |  | 100 | 155 | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR080000 | Manifold 8 | 2021-02-01 | 15:01 | 57.5 | 40.1 | 0.6 | 48 | 104 | 1.8 | 952 | -122.13 |  | 100 | 392 | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-02-08 | 13:45 | 56 | 40.6 | 1 | 57 | 57 | 2.4 | 958 | -194.01 |  | 100 | 386 | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR080000 | Manifold 8 | 2021-02-15 | 15:29 | 53.5 | 37.8 | 1.2 | 56 | 70 | 7.5 | 969 | -159.23 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-02-22 | 14:58 | 50.7 | 37.6 | 1 | 52 | 40 | 10.7 | 972 | -169.57 |  | 100 | 317 | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-03-02 | 14:49 | 50.7 | 37.4 | 0.9 | 51 | 45 | 11 | 981 | -171.99 |  | 100 | 378 | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR080000 | Manifold 8 | 2021-03-08 | 14:55 | 46.4 | 36.1 | 1.6 | 20 | 16 | 15.9 | 976 | -201.8 |  | 100 | 217 | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR080000 | Manifold 8 | 2021-03-16 | 12:50 | 50.1 | 35.7 | 1.4 | 83 | 36 | 12.8 | 982 | -184.36 |  | 100 | 525 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0% | WEST
TR080000 | Manifold 8 | 2021-03-25 | 13:27 | 57.7 | 39.6 | 0.7 | 75 | 49 | 2 | 970 | -176.83 |  | 100 | 302 | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 40% | SOUTH-WEST
TR080000 | Manifold 8 | 2021-03-30 | 13:33 | 56.2 | 39 | 0.6 | 65 | 52 | 4.2 | 981 | -171.8 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR080100 | man 8 line 1 | 2021-01-27 | 11:08 | 61.8 | 39 | 0.9 | 55 | 165 | 0 | 967 | -118.26 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR080100 | man 8 line 1 | 2021-02-08 | 13:47 | 58.4 | 40.9 | 1.7 | 55 | 70 | 0 | 956 | -190.54 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR080100 | man 8 line 1 | 2021-03-02 | 14:51 | 56.6 | 39.6 | 1.1 | 59 | 49 | 2.7 | 980 | -167.93 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR080101 | M8 L1 PL1 | 2021-02-16 | 15:18 | 52.9 | 38.3 | 0.8 | 9 | 17 | 8 | 958 | -111.97 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08011A | M8 L1 P1A | 2021-01-08 | 12:59 | 57.8 | 40.5 | 1.9 | 61 | 301 | 0 | 971 | -0.76 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-08 | 13:00 | 35.8 | 25.5 | 9 | 43 | 94 | 29.7 | 971 | -3.25 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-08 | 13:01 | 55.6 | 39.6 | 1.9 | 60 | 240 | 2.9 | 971 | -6.73 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-08 | 13:02 | 55.8 | 40 | 1.9 | 62 | 333 | 2.3 | 971 | -5.71 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-08 | 13:02 | 54.1 | 38.9 | 2.5 | 60 | 302 | 4.5 | 971 | -3.56 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-08 | 13:13 | 54.1 | 39.2 | 2.3 | 51 | 347 | 4.4 | 971 | -4.62 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011A | M8 L1 P1A | 2021-01-15 | 8:47 | 11.5 | 13 | 11.3 | 27 | 24 | 64.2 | 981 | -7.31 |  | 30 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011A | M8 L1 P1A | 2021-01-15 | 8:50 | 22.2 | 24 | 3.2 | 43 | 71 | 50.6 | 981 | -0.78 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011B | M8 L1 P1B | 2021-01-08 | 13:04 | 57.6 | 38.5 | 2.7 | 82 | 462 | 1.2 | 971 | -0.94 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011B | M8 L1 P1B | 2021-01-08 | 13:05 | 58.3 | 37.6 | 0.2 | 81 | 439 | 3.9 | 971 | -48.04 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011B | M8 L1 P1B | 2021-01-08 | 13:14 | 54 | 36.7 | 0.3 | 63 | 376 | 9 | 971 | -41.17 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011B | M8 L1 P1B | 2021-01-15 | 8:48 | 22.7 | 24.4 | 0.8 | 52 | 47 | 52.1 | 982 | -40.61 |  | 30 |  | Investigation/attention required |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011B | M8 L1 P1B | 2021-01-15 | 8:50 | 22.8 | 24.2 | 3.7 | 42 | 74 | 49.3 | 981 | -1.53 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011C | M8 L1 P1C | 2021-01-08 | 13:06 | 64 | 43.8 | 0.6 | 72 | 439 | 0 | 971 | -0.02 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011C | M8 L1 P1C | 2021-01-08 | 13:07 | 64 | 44.2 | 0.2 | 84 | 590 | 0 | 971 | -14.91 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011C | M8 L1 P1C | 2021-01-08 | 13:15 | 63.1 | 43.6 | 0.4 | 71 | 426 | 0 | 971 | -12.77 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011C | M8 L1 P1C | 2021-01-15 | 8:49 | 23.4 | 25.1 | 3.1 | 41 | 95 | 48.4 | 982 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011C | M8 L1 P1C | 2021-01-15 | 8:49 | 23.4 | 24.8 | 3.1 | 46 | 93 | 48.7 | 982 | -12.43 |  | 30 |  | Investigation/attention required |  |  | No | 1-3mph | FROZEN | NONE | 70% | EAST
TR08011D | M8 L1 P1D | 2021-01-08 | 13:11 | 55.6 | 38.5 | 0.4 | 88 | 208 | 5.5 | 970 | -115.17 |  | 100 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08011D | M8 L1 P1D | 2021-01-15 | 8:51 | 53 | 37.9 | 0.3 | 89 | 192 | 8.8 | 981 | -121.35 |  | 100 |  | Odour/migration control |  |  | N/A | 1-3mph | FROZEN | NONE | 70% | EAST
TR080200 | man 8 line 2 | 2021-01-27 | 11:09 | 52.5 | 37.7 | 1.5 | 41 | 108 | 8.3 | 966 | -123.86 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 100% | NORTH-EAST
TR080200 | man 8 line 2 | 2021-02-08 | 13:48 | 53.5 | 39.8 | 1 | 44 | 70 | 5.7 | 956 | -193.09 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 80% | NORTH-EAST
TR080200 | man 8 line 2 | 2021-03-02 | 14:52 | 47.5 | 36 | 1 | 49 | 45 | 15.5 | 981 | -169.38 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR080201 | M8 L2 pin line 1 | 2021-02-16 | 15:20 | 0.1 | 0.2 | 21.1 | 0 | 0 | 78.6 | 959 | -113.61 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR080202 | M8 L2 pin line 2 | 2021-02-16 | 15:27 | 60.2 | 41 | 0.3 | 21 | 404 | 0 | 958 | -56.73 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08021A | M8 L2 pin line 1A | 2021-02-16 | 15:25 | 55.4 | 35 | 1.2 | 17 | 124 | 8.4 | 960 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08021A | M8 L2 pin line 1A | 2021-02-16 | 15:26 | 47.9 | 34.7 | 0.8 | 22 | 97 | 16.6 | 960 | -6.13 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08021A | M8 L2 pin line 1A | 2021-02-16 | 15:26 | 46.2 | 33.5 | 0.8 | 22 | 90 | 19.5 | 960 | -0.76 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08021B | M8 L2 pin line 1B | 2021-02-16 | 15:23 | 59.8 | 39.5 | 0.8 | 10 | 34 | 0 | 958 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08021B | M8 L2 pin line 1B | 2021-02-16 | 15:24 | 54.7 | 37.9 | 0.2 | 12 | 62 | 7.2 | 958 | -1.42 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR08023B | M8 L2 W3B | 2021-03-08 | 14:17 | 16 | 20.1 | 2.1 | 36 | 5 | 61.8 | 977 | -9.04 |  | 20 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR08023B | M8 L2 W3B | 2021-03-08 | 14:17 | 15.7 | 20.3 | 2 | 34 | 6 | 62 | 977 | -0.59 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR08023C | M8 L2 W3C | 2021-03-08 | 14:11 | 67.1 | 42.1 | 0.1 | 89 | 12 | 0 | 975 | 0.66 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR08023C | M8 L2 W3C | 2021-03-08 | 14:12 | 49.7 | 35.6 | 0.2 | 72 | 12 | 14.5 | 977 | -0.42 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR08023C | M8 L2 W3C | 2021-03-08 | 14:13 | 48.9 | 35.2 | 0.2 | 71 | 16 | 15.7 | 977 | -0.49 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR08023D | PIN WELLS | 2021-01-08 | 12:51 | 39.5 | 31.1 | 0.4 | 50 | 27 | 29 | 970 | -2.78 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08023D | PIN WELLS | 2021-01-08 | 12:52 | 38.9 | 30.8 | 0.4 | 44 | 24 | 29.9 | 970 | -0.62 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR08023E | PIN WELLS | 2021-01-08 | 12:50 | 50.1 | 38.6 | 0.8 | 60 | 32 | 10.5 | 972 | -4.23 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR080300 | man 8 line 3 | 2021-01-07 | 16:21 | 56.1 | 37.4 | 2.2 | 31 | 64 | 4.3 | 970 | -132.71 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR080300 | man 8 line 3 | 2021-02-15 | 15:25 | 51.8 | 36.9 | 1.6 | 56 | 59 | 9.7 | 971 | -158.14 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR080300 | man 8 line 3 | 2021-03-02 | 14:53 | 51.7 | 36.7 | 1.2 | 48 | 84 | 10.4 | 981 | -176.53 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR08030A | M8 L3 LA | 2021-02-16 | 15:19 | 0.1 | 0.2 | 20.6 | 0 | 0 | 79.1 | 961 | -0.26 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0803A0 | M8 L3A | 2021-01-08 | 14:35 | 54.5 | 37 | 2.6 | 32 | 42 | 5.9 | 971 | -108.92 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A0 | M8 L3A | 2021-02-15 | 15:26 | 54.5 | 36.4 | 1.1 | 51 | 50 | 8 | 969 | -163.78 |  | 100 |  | Odour/migration control |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0803A0 | M8 L3A | 2021-03-02 | 14:54 | 52.8 | 36.7 | 1.1 | 49 | 57 | 9.4 | 980 | -171.1 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803A1 | M8 L3 LA pin line 1 | 2021-01-08 | 14:44 | 49.3 | 32.1 | 1.3 | 22 | 72 | 17.3 | 971 | -0.5 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A2 | M8 L2 LA pin line 2 | 2021-01-08 | 14:45 | 51 | 33.7 | 0.3 | 27 | 131 | 15 | 970 | -31.53 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A2 | M8 L2 LA pin line 2 | 2021-01-08 | 14:46 | 52.3 | 33.9 | 0 | 36 | 172 | 13.8 | 970 | -34.92 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A2 | M8 L2 LA pin line 2 | 2021-03-02 | 14:37 | 25.1 | 25.1 | 0.4 | 33 | 87 | 49.4 | 980 | -127.45 |  | 30 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803A2 | M8 L2 LA pin line 2 | 2021-03-02 | 14:38 | 25.1 | 25.6 | 0.4 | 35 | 95 | 48.9 | 980 | -9.93 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803A2 | M8 L2 LA pin line 2 | 2021-03-08 | 14:44 | 77.6 | 43.7 | 0.7 | 86 | 479 |  | 975 | 0.17 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | WEST
TR0803A2 | M8 L2 LA pin line 2 | 2021-03-08 | 14:45 | 61 | 36.9 | 0.1 | 75 | 110 | 2 | 975 | -37.04 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR0803A3 | M8 L2 LA pin line 3 | 2021-01-08 | 14:48 | 56.3 | 36 | 0.9 | 40 | 66 | 6.8 | 970 | -0.43 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A3 | M8 L2 LA pin line 3 | 2021-01-08 | 14:49 | 54.3 | 34.3 | 0.7 | 39 | 51 | 10.7 | 970 | -11.54 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A3 | M8 L2 LA pin line 3 | 2021-03-02 | 14:36 | 12.8 | 14.3 | 8.4 | 41 | 10 | 64.5 | 978 | -17.32 |  | 20 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803A3 | M8 L2 LA pin line 3 | 2021-03-02 | 14:36 | 12.2 | 14.2 | 8.5 | 33 | 8 | 65.1 | 978 | -0.28 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803A4 | M8 L3 LA pin line 4 | 2021-01-08 | 14:50 | 42.9 | 30.7 | 4.6 | 30 | 46 | 21.8 | 971 | -0.26 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803A5 | M8 L3 LA pin line 5 | 2021-01-08 | 14:51 | 40.7 | 26.1 | 3.5 | 25 | 24 | 29.7 | 971 | -0.45 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803B0 | M8 L3B | 2021-01-08 | 14:40 | 1.1 | 0.7 | 21.5 | 9 | 1 | 76.7 | 972 | -0.4 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803B0 | M8 L3B | 2021-02-15 | 15:28 | 1.2 | 0.7 | 21.7 | 19 | 12 | 76.4 | 972 | 0.02 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 100% | SOUTH-WEST
TR0803B0 | M8 L3B | 2021-03-02 | 14:55 | 0.1 | 0.2 | 20.1 | 24 | 18 | 79.6 | 980 | -0.05 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 20% | NORTH-EAST
TR0803C0 | M8 L3C | 2021-01-08 | 14:41 | 60.2 | 38.9 | 0.9 | 23 | 570 | 0 | 969 | -78.18 |  | 100 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0803C0 | M8 L3C | 2021-02-16 | 15:15 | 40.1 | 30.8 | 2.7 | 11 | 39 | 26.4 | 959 | -139.13 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 40% | SOUTH-WEST
TR0803C0 | M8 L3C | 2021-03-08 | 14:47 | 60 | 37.5 | 0.8 | 38 | 17 | 1.7 | 977 | -196.39 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR0803C1 | M8 L3 Lc pin line 1 | 2021-01-29 | 14:47 | 67.9 | 40.7 | 0.3 | 22 | 83 | 0 | 953 | -2.27 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0803C1 | M8 L3 Lc pin line 1 | 2021-01-29 | 14:48 | 69.2 | 41.3 | 0.2 | 26 | 143 |  | 953 | -4.1 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0803D0 | 160MM TO MAN 8 L3 | 2021-01-29 | 14:51 | 57.8 | 38.3 | 2 | 17 | 311 | 1.9 | 954 | -35.7 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0803D0 | 160MM TO MAN 8 L3 | 2021-01-29 | 14:52 | 62.3 | 41.3 | 0.5 | 17 | 502 | 0 | 954 | -108.97 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0803F0 | MAN8 LINE3 LINE F | 2021-01-29 | 14:46 | 60.1 | 31.6 | 0.2 | 13 | 8 | 8.1 | 953 | -98.98 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0811C1 | M8 PIN1 | 2021-01-08 | 13:09 | 17.7 | 13.7 | 15 | 32 | 57 | 53.6 | 969 | 0.09 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0811C2 | M8 PIN2 | 2021-01-08 | 13:10 | 15.8 | 10.1 | 16.7 | 29 | 39 | 57.4 | 970 | 0.03 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 50% | NORTH-EAST
TR0P90MM | Line P 90mm line | 2021-03-15 | 15:20 | 5.2 | 4.2 | 18.5 | 10 | 1 | 72.1 | 980 | -0.56 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0% | WEST
TR0P90MM | Line P 90mm line | 2021-03-30 | 12:47 | 19.4 | 20 | 4.3 | 9 | 1 | 56.3 | 984 | -0.05 |  | 0 |  | Gas depletes when adjusted |  |  | No | 4-7mph | DRYING | NONE | 10% | NORTH-EAST
TR0W0PN1 | line W pin well line 1 | 2021-03-08 | 15:24 | 63.5 | 37.3 | 0.1 | 7 | 4 | 0 | 976 | -20.34 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 20% | WEST
TR0W0PN2 | line W pin well line 2 | 2021-01-29 | 12:51 | 19.3 | 3.1 | 15.2 | 34 | 345 | 62.4 | 951 | -12.89 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 80% | SOUTH-WEST
TR0W0PN2 | line W pin well line 2 | 44225 | 0.5375 | 58.2 | 38.3 | 0.5 | 64 | 12 | 3 | 952 | -20.24 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TR0W0PN2 | line W pin well line 2 | 44263 | 0.63681 | 69.8 | 29.5 | 0.2 | 9 | 3 | 0.5 | 976 | -5 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | WEST
TR0W0PN2 | line W pin well line 2 | 44263 | 0.63681 | 69 | 27.9 | 0.7 | 10 | 3 | 2.4 | 976 | -0.76 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | WEST
TR0W0PN3 | line W pin well line 3 | 44263 | 0.63958 | 71.3 | 30.4 | 0 | 8 | 36 | 0 | 978 | 126.07 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | WEST
TR0W0PN3 | line W pin well line 3 | 44263 | 0.64028 | 70.4 | 31.8 | 0 | 7 | 26 | 0 | 978 | -5.14 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | WEST
TR0WPINS | LINE W PIN WELLS | 44214 | 0.63889 | 0.5 | 0.3 | 21.3 | 17 | 22 | 77.9 | 972 | -90.82 |  | 10 |  | gas carrier flooded | 10 | GTE Line flooded | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR0WPINS | LINE W PIN WELLS | 44249 | 0.62847 | 0 | 0.2 | 19 | 17 | 44 | 80.8 | 969 | -58.3 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TR0WPINS | LINE W PIN WELLS | 44263 | 0.63611 | 3.1 | 14.3 | 17.3 | 6 | 3 | 65.3 | 978 | -67.88 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 0.2 | WEST
TR100201 | M10 L2 pin Line 1 | 44204 | 0.52778 | 64.6 | 40.5 | 0.6 | 23 | 5 | 0 | 969 | -0.62 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100201 | M10 L2 pin Line 1 | 44204 | 0.52847 | 65.4 | 40.6 | 0.2 | 29 | 20 | 0 | 969 | -0.85 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100201 | M10 L2 pin Line 1 | 44270 | 0.625 | 13.5 | 18.2 | 2.1 | 15 | 11 | 66.2 | 976 | -3.73 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100201 | M10 L2 pin Line 1 | 44270 | 0.625 | 13.1 | 18.2 | 2 | 14 | 11 | 66.7 | 976 | -0.95 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100202 | M10 L2 pin line 2 | 44204 | 0.52917 | 49.3 | 30.8 | 1.5 | 29 | 25 | 18.4 | 970 | -11.51 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100202 | M10 L2 pin line 2 | 44270 | 0.62431 | 11.3 | 13.7 | 5.4 | 26 | 7 | 69.6 | 976 | -10.45 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100202 | M10 L2 pin line 2 | 44270 | 0.62431 | 10.8 | 13.3 | 5.4 | 25 | 6 | 70.5 | 976 | -5.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100203 | M10 L2 pin line 3 | 44204 | 0.52986 | 50.3 | 31.2 | 0.3 | 28 | 17 | 18.2 | 969 | -25.79 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100203 | M10 L2 pin line 3 | 44270 | 0.62292 | 19.3 | 19.2 | 2.3 | 24 | 10 | 59.2 | 976 | -25.74 |  | 20 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100203 | M10 L2 pin line 3 | 44270 | 0.62361 | 18.7 | 19.1 | 2.2 | 23 | 11 | 60 | 976 | -6.28 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100204 | MAN 10 LINE 2 PIN LINE 4 | 44204 | 0.53056 | 48.6 | 34 | 0.6 | 36 | 14 | 16.8 | 970 | -0.23 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100204 | MAN 10 LINE 2 PIN LINE 4 | 44270 | 0.62153 | 16.9 | 16.6 | 4.6 | 35 | 9 | 61.9 | 976 | -6.25 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100204 | MAN 10 LINE 2 PIN LINE 4 | 44270 | 0.62222 | 16.3 | 16.2 | 4.6 | 34 | 10 | 62.9 | 976 | -2.03 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100205 | PIN WELLS | 44204 | 0.53125 | 59.1 | 38.5 | 0.1 | 67 | 124 | 2.3 | 970 | -36.6 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100205 | PIN WELLS | 44204 | 0.53194 | 60.4 | 37.8 | 0.1 | 72 | 140 | 1.7 | 970 | -44.6 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100205 | PIN WELLS | 44270 | 0.62083 | 19.9 | 21.4 | 2.8 | 29 | 7 | 55.9 | 977 | -36.5 |  | 20 |  | Investigation/attention required |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100205 | PIN WELLS | 44270 | 0.62083 | 19 | 21 | 2.8 | 25 | 6 | 57.2 | 977 | -0.47 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100206 | M10 L2 P6 | 44204 | 0.53264 | 62.4 | 38.3 | 0.5 | 61 | 79 | 0 | 970 | -26.99 |  | 25 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100206 | M10 L2 P6 | 44204 | 0.53333 | 61.9 | 38.8 | 0.2 | 68 | 122 | 0 | 970 | -42.24 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR100206 | M10 L2 P6 | 44270 | 0.61944 | 41.7 | 32.4 | 0.8 | 33 | 15 | 25.1 | 976 | -46.49 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR100206 | M10 L2 P6 | 44270 | 0.61944 | 40.7 | 32 | 0.8 | 36 | 20 | 26.5 | 976 | -12.04 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR100206 | M10 L2 P6 | 44270 | 0.62569 | 41.2 | 32.2 | 0.9 | 30 | 12 | 25.7 | 978 | -3.66 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TR10307A | M1 L3 PL7A | 44204 | 0.58403 | 66.1 | 36.1 | 1 | 20 | 52 | 0 | 971 | 0.59 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR10307A | M1 L3 PL7A | 44204 | 0.60069 | 5.2 | 3.7 | 19.7 | 6 | 0 | 71.4 | 969 | -30.93 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR10307A | M1 L3 PL7A | 44204 | 0.60069 | 4 | 3.2 | 20.1 | 6 | 0 | 72.7 | 969 | -1.25 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110000 | Manifold 11 | 44200 | 0.59583 | 44.8 | 31.6 | 2.2 | 37 | 76 | 21.4 | 972 | -160.91 |  | 100 | 170 | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110000 | Manifold 11 | 44211 | 0.37986 | 42.7 | 30.7 | 2.2 | 34 | 204 | 24.4 | 982 | -134.17 |  | 100 |  | Odour/migration control |  |  | No | 1-3mph | FROZEN | NONE | 0.7 | EAST
TR110000 | Manifold 11 | 44214 | 0.64583 | 43.8 | 31.1 | 2.5 | 31 | 123 | 22.6 | 971 | -137.8 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110000 | Manifold 11 | 44221 | 0.63056 | 48 | 33.1 | 3 | 22 | 227 | 15.9 | 966 | -167.35 |  | 100 | 121 | Condition good |  |  | No | 8-11mph | SNOW COVERED | NONE | 1 | NORTH-EAST
TR110000 | Manifold 11 | 44228 | 0.64028 | 51.2 | 32.8 | 3.9 | 31 | 460 | 12.1 | 955 | -157.63 |  | 100 | 53 | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TR110000 | Manifold 11 | 44235 | 0.5875 | 54 | 36.1 | 2.9 | 25 | 395 | 7 | 956 | -198.28 |  | 100 | 112 | Condition good |  |  | No | 19-24mph | FROZEN | SNOW | 0.8 | NORTH-EAST
TR110000 | Manifold 11 | 44243 | [12 empty] | LANDFILL PROJECTS WORKING CLOSE BY | 6 | No safe access | N/A | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TR110000 | Manifold 11 | 44249 | 0.63333 | 47.5 | 33.4 | 2 | 23 | 100 | 17.1 | 971 | -171.69 |  | 100 | 110 | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TR110000 | Manifold 11 | 44257 | 0.63611 | 49.3 | 34.5 | 1.9 | 21 | 139 | 14.3 | 983 | -207.17 |  | 100 | 0 | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TR110000 | Manifold 11 | 44263 | 0.64653 | 38.7 | 32.3 | 1.8 | 7 | 2 | 27.2 | 975 | -199.74 |  | 100 | 8 | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 0.2 | WEST
TR110000 | Manifold 11 | 44271 | 0.54792 | 41.3 | 30.4 | 2.2 | 31 | 44 | 26.1 | 984 | -185.8 |  | 100 | 72 | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR110000 | Manifold 11 | 44280 | 0.57361 | 46.6 | 33.7 | 1 | 35 | 149 | 18.7 | 972 | -180.96 |  | 100 | 90 | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110000 | Manifold 11 | 44285 | 0.57431 | 44.8 | 31.9 | 1 | 45 | 114 | 22.3 | 981 | -175.96 |  | 100 |  | Odour/migration control |  |  | No | 4-7mph | DRYING | NONE | 0.1 | NORTH-EAST
TR110100 | Manifold 11, line 1 | 44214 | 0.64722 | 63.2 | 40.4 | 0.3 | 26 | 65 | 0 | 969 | -138.15 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110100 | Manifold 11, line 1 | 44235 | 0.58889 | 61.6 | 41.4 | 0.6 | 16 | 116 | 0 | 955 | -198.4 |  | 50 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 0.8 | NORTH-EAST
TR110100 | Manifold 11, line 1 | 44257 | 0.63889 | 64 | 40 | 0.1 | 33 | 505 | 0 | 980 | -206.07 |  | 50 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TR110200 | M11 L2 | 44214 | 0.64861 | 53.5 | 40.8 | 0.8 | 31 | 83 | 4.9 | 969 | -136.5 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110200 | M11 L2 | 44235 | 0.58958 | 56.9 | 42.6 | 1.6 | 23 | 80 | 0 | 956 | -196.75 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | FROZEN | SNOW | 0.8 | NORTH-EAST
TR110200 | M11 L2 | 44257 | 0.64028 | 57.6 | 43.3 | 0.4 | 25 | 94 | 0 | 980 | -204.6 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TR110200 | M11 L2 | 44257 | 0.64097 | 57.9 | 43.2 | 0.2 | 28 | 72 | 0 | 980 | -203.64 |  | 50 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TR110300 | M11 L3 | 44204 | 0.57083 | 44.9 | 31.5 | 1.7 | 40 | 263 | 21.9 | 970 | -120.51 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110300 | M11 L3 | 44214 | 0.65 | 44 | 31.3 | 1.7 | 38 | 219 | 23 | 969 | -137.4 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110300 | M11 L3 | 44249 | 0.63611 | 47.3 | 33.2 | 2 | 23 | 128 | 17.5 | 969 | -71.48 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TR110300 | M11 L3 | 44271 | 0.55208 | 32 | 23.7 | 6.2 | 28 | 68 | 38.1 | 981 | -187.29 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0 | WEST
TR110300 | M11 L3 | 44274 | 0.62778 | 44.7 | 31.7 | 2.5 | 32 | 52 | 21.1 | 984 | -209.32 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110301 | M11 L3 PL1 | 44204 | 0.56944 | 0.8 | 0.5 | 22 | 15 | 12 | 76.7 | 971 | -2 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110302 | M11 L3 PIN LINE 2 | 44204 | 0.56736 | 50.4 | 34.8 | 0.9 | 42 | 221 | 13.9 | 968 | -2.46 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110302 | M11 L3 PIN LINE 2 | 44214 | 0.65764 | 34.1 | 26.9 | 3.6 | 23 | 63 | 35.4 | 968 | -0.02 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110302 | M11 L3 PIN LINE 2 | 44214 | 0.65764 | 33.5 | 26.8 | 2.7 | 23 | 73 | 37 | 968 | -0.09 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110302 | M11 L3 PIN LINE 2 | 44274 | 0.61736 | 63.5 | 42.5 | 0.4 | 51 | 501 | 0 | 983 | -0.61 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110302 | M11 L3 PIN LINE 2 | 44274 | 0.61806 | 63.6 | 40 | 0.1 | 55 | 481 | 0 | 983 | -2.24 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110303 | M11 L3 PIN LINE 3 | 44204 | 0.56597 | 44.6 | 32.9 | 0.7 | 42 | 457 | 21.8 | 969 | -3.87 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110303 | M11 L3 PIN LINE 3 | 44214 | 0.65833 | 35.5 | 29.5 | 0.9 | 29 | 287 | 34.1 | 968 | -5.1 |  | 10 |  | Investigation/attention required |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110303 | M11 L3 PIN LINE 3 | 44214 | 0.65903 | 34.8 | 29.2 | 0.8 | 28 | 314 | 35.2 | 968 | -1.42 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110303 | M11 L3 PIN LINE 3 | 44274 | 0.61875 | 60.7 | 38.1 | 0.6 | 44 | 426 | 0.6 | 983 | -0.57 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110303 | M11 L3 PIN LINE 3 | 44274 | 0.61875 | 60.2 | 38.1 | 0.6 | 43 | 439 | 1.1 | 983 | -5.9 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110304 | M11 L3 PIN LINE 4 | 44204 | 0.56528 | 42.1 | 31.7 | 0.5 | 42 | 364 | 25.7 | 963 | -3.37 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110304 | M11 L3 PIN LINE 4 | 44214 | 0.65972 | 39.8 | 30.3 | 1.2 | 34 | 287 | 28.7 | 969 | -3.63 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110304 | M11 L3 PIN LINE 4 | 44214 | 0.65972 | 39.1 | 30 | 1.1 | 33 | 268 | 29.8 | 969 | -2.97 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110304 | M11 L3 PIN LINE 4 | 44274 | 0.61944 | 65.6 | 38.8 | 0.4 | 43 | 627 | 0 | 983 | -0.56 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110304 | M11 L3 PIN LINE 4 | 44274 | 0.62014 | 65.4 | 38.6 | 0.2 | 48 | 746 | 0 | 983 | -8.4 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110305 | M11 L3 PIN LINE 5 | 44204 | 0.56389 | 48.3 | 30.8 | 2.8 | 47 | 352 | 18.1 | 968 | -2.57 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110305 | M11 L3 PIN LINE 5 | 44214 | 0.66042 | 46.8 | 30.7 | 2.5 | 38 | 355 | 20 | 969 | -2.69 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110305 | M11 L3 PIN LINE 5 | 44274 | 0.61528 | 65.4 | 42.2 | 0.3 | 44 | 694 | 0 | 982 | -0.64 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110305 | M11 L3 PIN LINE 5 | 44274 | 0.61597 | 65.5 | 41.4 | 0.1 | 53 | 862 | 0 | 982 | -1.6 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110305 | M11 L3 PIN LINE 5 | 44274 | 0.62083 | 60.6 | 39.1 | 0.4 | 57 | 767 | 0 | 983 | -0.97 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110306 | M11 L3 PIN WELL 6 | 44204 | 0.5625 | 38.3 | 26.8 | 2.5 | 44 | 92 | 32.4 | 970 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110307 | M11 L3 PIN WELL 7 | 44204 | 0.56111 | 74.9 | 41.7 | 0.3 | 65 | 971 |  | 970 | -66.52 |  | 20 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110307 | M11 L3 PIN WELL 7 | 44204 | 0.56181 | 75.5 | 41.9 | 0.1 | 74 | 1148 |  | 970 | -113 |  | 30 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110307 | M11 L3 PIN WELL 7 | 44214 | 0.66111 | 59.1 | 37 | 1.4 | 38 | 396 | 2.5 | 968 | -102.29 |  | 30 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110307 | M11 L3 PIN WELL 7 | 44274 | 0.62292 | 44.6 | 32.4 | 1.3 | 30 | 168 | 21.7 | 981 | -68.36 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110308 | M11 L3 PIN WELL 8 | 44204 | 0.55972 | 55.9 | 35.7 | 0.6 | 52 | 386 | 7.8 | 969 | -20.46 |  | 50 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110308 | M11 L3 PIN WELL 8 | 44204 | 0.56042 | 56.3 | 35.7 | 0.6 | 52 | 414 | 7.4 | 969 | -25.93 |  | 60 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110308 | M11 L3 PIN WELL 8 | 44214 | 0.66181 | 49.4 | 32.9 | 1.6 | 43 | 371 | 16.1 | 968 | -19.52 |  | 60 |  | Condition good |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110308 | M11 L3 PIN WELL 8 | 44274 | 0.62361 | 60.8 | 35.7 | 0.3 | 44 | 229 | 3.2 | 975 | -151.61 |  | 60 |  | Condition good |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110308 | M11 L3 PIN WELL 8 | 44274 | 0.62431 | 61.3 | 35.9 | 0.2 | 48 | 345 | 2.6 | 975 | -154.91 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TR110309 | M11 L3 PIN WELL 9 | 44204 | 0.55903 | 42.3 | 30.8 | 0.9 | 41 | 140 | 26 | 968 | -57.74 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110309 | M11 L3 PIN WELL 9 | 44214 | 0.66319 | 37.9 | 29 | 1 | 39 | 185 | 32.1 | 969 | -68.38 |  | 30 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110309 | M11 L3 PIN WELL 9 | 44214 | 0.66319 | 37.2 | 29.1 | 0.9 | 36 | 162 | 32.8 | 969 | -7.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR110310 | M11 L3 PIN WELL 10 | 44204 | 0.55764 | 40.4 | 26.7 | 5.8 | 31 | 51 | 27.1 | 968 | -6.3 |  | 10 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR110310 | M11 L3 PIN WELL 10 | 44204 | 0.55764 | 39.6 | 26.6 | 5.6 | 30 | 56 | 28.2 | 968 | -0.99 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR1103SC | M11 L3 SCAVENGER | 44204 | 0.56806 | 18.7 | 15.4 | 10.2 | 26 | 28 | 55.7 | 970 | -0.19 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TR5LINE1 | Man5 line 1 | 44214 | 0.61875 | 51.1 | 34.5 | 0.4 | 82 | 614 | 14 | 969 | -135.73 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TR5LINE1 | Man5 line 1 | 44242 | 0.61458 | 35.9 | 28.5 | 1.7 | 50 | 228 | 33.9 | 969 | -158.24 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TR5LINE1 | Man5 line 1 | 44242 | 0.62083 | 36.1 | 26.4 | 0.7 | 34 | 149 | 36.8 | 970 | -165.22 |  | 100 |  | Investigation/attention required |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TR5LINE1 | Man5 line 1 | 44263 | 0.60764 | 45.4 | 32.9 | 0.6 | 86 | 931 | 21.1 | 977 | -205.64 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 0.2 | WEST
TR5LINE1 | Man5 line 1 | 44285 | 0.62222 | 28 | 21.8 | 2.8 | 29 | 11 | 47.4 | 981 | -174.75 |  | 100 |  | Investigation/attention required |  |  | No | 4-7mph | DRYING | NONE | 0.1 | NORTH-EAST
TR5LINE1 | Man5 line 1 | 44285 | 0.62639 | 19.4 | 14.4 | 9 | 25 | 7 | 57.2 | 978 | -175.22 |  | 100 |  | Odour/migration control |  |  | N/A | 4-7mph | DRYING | NONE | 0.1 | NORTH-EAST
TRK160MM | sample point K 160mm line | 44223 | 0.42847 | 53.2 | 36.5 | 2.1 | 21 | 60 | 8.2 | 964 | -145.87 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | SNOW COVERED | NONE | 1 | NORTH-EAST
TRK160MM | sample point K 160mm line | 44243 | 0.44514 | 54.6 | 37.3 | 1.8 | 35 | 27 | 6.3 | 958 | -188.27 |  | 100 |  | Condition good |  |  | N/A | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRK160MM | sample point K 160mm line | 44280 | 0.62708 | 58.2 | 40.9 | 1.9 | 74 | 62 | 0 | 967 | -183.58 |  | 100 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRLW4PN1 | leachate W4/pin well line 1 | 44228 | 0.61181 | 34.5 | 34.3 | 0.4 | 7 | 101 | 30.8 | 951 | -2.39 |  | 30 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRLW4PN1 | leachate W4/pin well line 1 | 44228 | 0.6125 | 34 | 34.4 | 0.2 | 6 | 103 | 31.4 | 951 | -1.18 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRLW4PN1 | leachate W4/pin well line 1 | 44230 | 0.5375 | 32.8 | 30.7 | 2.1 | 10 | 18 | 34.4 | 948 | -0.14 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRLW4PN2 | pin well lines | 44243 | 0.44583 | 44.2 | 34.3 | 0.7 | 17 | 8 | 20.8 | 958 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRMPBSR1 | MPB line side riser 1 | 44258 | 0.56111 | 64.5 | 34.1 | 0.3 | 0 | 18 | 1.1 | 981 | -0.07 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRMPBSR2 | MPB line side riser 2 | 44258 | 0.56181 | 78.1 | 22.8 | 0.2 | 0 | 8 | 0 | 980 | -0.3 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRMPBSR2 | MPB line side riser 2 | 44258 | 0.5625 | 78.6 | 22.6 | 0.3 | 0 | 10 | 0 | 980 | -0.56 |  | 20 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRO355MM | Line "O" 355MM line | 44200 | 0.56597 | 47.9 | 33.8 | 1 | 20 | 3 | 17.3 | 972 | -164.28 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRO355MM | Line "O" 355MM line | 44203 | 0.68681 | 48.8 | 34.9 | 0.8 | 20 | 33 | 15.5 | 969 | -155.07 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRO355MM | Line "O" 355MM line | 44242 | 0.57708 | 41 | 31.4 | 0.8 | 12 | 6 | 26.8 | 969 | -157.3 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRO355MM | Line "O" 355MM line | 44270 | 0.64028 | 49.8 | 35.5 | 0.8 | 20 | 24 | 13.9 | 977 | -194.65 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0 | WEST
TRO355MM | Line "O" 355MM line | 44285 | 0.53194 | 51.1 | 35.2 | 0.8 | 15 | 1 | 12.9 | 980 | -184.2 |  | 100 |  | Condition good |  |  | N/A | 4-7mph | DRYING | NONE | 0.1 | NORTH-EAST
TROLD4SR | OLD MAN4 SR LINES | 44260 | 0.56111 | 27.1 | 18.5 | 10.7 | 2 | 1 | 43.7 | 984 | -0.85 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TROLD4SR | OLD MAN4 SR LINES | 44260 | 0.56111 | 25.7 | 17.4 | 11.6 | 2 | 1 | 45.3 | 984 | -1.89 |  | 10 |  | Gas depletes when adjusted |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRSTMPPN | stamper lagoon pins | 44204 | 0.58125 | 25.6 | 13.8 | 13.9 | 19 | 12 | 46.7 | 971 | -0.33 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRT355MM | Line T 355mm line | 44218 | 0.40347 | 52.8 | 36.1 | 2 | 53 | 395 | 9.1 | 943 | -190 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TRT355MM | Line T 355mm line | 44242 | 0.66944 | 46.8 | 34.5 | 1.4 | 46 | 282 | 17.3 | 970 | -173.81 |  | 100 |  | Condition good |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRT355MM | Line T 355mm line | 44258 | 0.6 | 46.1 | 34.4 | 1.3 | 30 | 221 | 18.2 | 980 | -182.3 |  | 100 |  | Condition good |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRU0PIN1 | PIN LINE 1 | 44253 | 0.58889 | 61.5 | 41.6 | 0.7 | 70 | 1439 | 0 | 987 | -178.79 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIN1 | PIN LINE 1 | 44274 | 0.58611 | 59.1 | 39.6 | 0.6 | 0 | 18 | 0.7 | 980 | -183.3 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PIN2 | PIN LINE 2 | 44253 | 0.57917 | 47.1 | 35.7 | 0.7 | 40 | 2 | 16.5 | 987 | -0.36 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIN2 | PIN LINE 2 | 44274 | 0.59722 | 59.1 | 40.1 | 0.1 | 20 | 4 | 0.7 | 980 | -39.34 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PIN2 | PIN LINE 2 | 44274 | 0.59792 | 56.5 | 43.6 | 0.1 | 15 | 4 | 0 | 980 | -105.69 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44225 | 0.54861 | 40.7 | 31.9 | 3.1 | 69 | 1 | 24.3 | 953 | -0.17 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44225 | 0.54931 | 31 | 28.9 | 1.4 | 68 | 3 | 38.7 | 953 | -0.4 |  | 10 |  | Investigation/attention required |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44225 | 0.54931 | 30 | 28.3 | 1.3 | 66 | 4 | 40.4 | 953 | -0.26 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44253 | 0.56736 | 69.3 | 35.6 | 0.4 | 26 | 171 | 0 | 988 | -0.07 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44253 | 0.56806 | 69.2 | 36 | 0.1 | 34 | 279 | 0 | 988 | -0.28 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44260 | 0.56597 | 26 | 24.2 | 2.5 | 39 | 48 | 47.3 | 984 | -1.2 |  | 10 |  | Investigation/attention required |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRU0PINA | PIN LINE A | 44260 | 0.56597 | 25.5 | 24.2 | 2.3 | 39 | 37 | 48 | 984 | -0.68 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRU0PINA | PIN LINE A | 44274 | 0.57847 | 31.3 | 26.8 | 1.9 | 0 | 12 | 40 | 981 | -0.28 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINA | PIN LINE A | 44274 | 0.57986 | 62 | 33.1 | 0.2 | 2 | 9 | 4.7 | 981 | -0.69 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44225 | 0.54653 | 49.7 | 34.3 | 1.1 | 57 | 1 | 14.9 | 952 | -7.84 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44225 | 0.54722 | 49.4 | 35.7 | 0.9 | 76 | 1 | 14 | 952 | -15.08 |  | 35 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44232 | 0.59097 | 48.5 | 34.8 | 1.6 | 88 | 706 | 15.1 | 956 | -12.53 |  | 30 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44253 | 0.56875 | 25.5 | 18.9 | 8.6 | 44 | 99 | 47 | 990 | -57.79 |  | 50 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44253 | 0.56944 | 43 | 29.6 | 4.3 | 86 | 380 | 23.1 | 990 | -1.61 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44253 | 0.57083 | 37.6 | 26.6 | 5.4 | 72 | 346 | 30.4 | 990 | -1.93 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44253 | 0.57153 | 48.3 | 32.3 | 2.7 | 89 | 455 | 16.7 | 990 | -0.05 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44274 | 0.58056 | 66.3 | 32.2 | 0.7 | 5 | 7 | 0.8 | 983 | -1.61 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINB | PIN LINE B | 44274 | 0.58125 | 62.1 | 39.3 | 0.1 | 10 | 7 | 0 | 983 | -3 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44225 | 0.53958 | 46.5 | 33.1 | 5.3 | 35 | 5 | 15.1 | 952 | 0.43 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44225 | 0.54028 | 56.7 | 36 | 1.8 | 89 | 9 | 5.5 | 952 | -1.11 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44253 | 0.575 | 36.9 | 8.1 | 1.9 | 30 | 7 | 53.1 | 987 | -27.63 |  | 10 |  | Investigation/attention required |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44253 | 0.575 | 36.7 | 9.5 | 1.4 | 32 | 7 | 52.4 | 987 | -15.69 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44274 | 0.58958 | 68.8 | 32.5 | 0.4 | 68 | 13 | 0 | 980 | -12.36 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44274 | 0.58958 | 67.8 | 32.1 | 0.2 | 49 | 12 | 0 | 980 | -0.12 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PINC | PIN LINE C | 44274 | 0.59236 | 71.2 | 26.7 | 1 | 41 | 5 | 1.1 | 980 | -9.55 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44253 | 0.58472 | 11.8 | 17.4 | 12.8 | 21 | 0 | 58 | 987 | -0.02 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44253 | 0.58542 | 10.5 | 10.3 | 15.5 | 18 | 0 | 63.7 | 987 | -22.02 |  | 20 |  | Odour/migration control |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44253 | 0.58542 | 10.4 | 12.2 | 14.9 | 17 | 0 | 62.5 | 987 | -1.54 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44253 | 0.58611 | 10.1 | 10 | 15.5 | 18 | 0 | 64.4 | 987 | -0.1 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44274 | 0.59097 | 1 | 7.7 | 19.7 | 13 | 6 | 71.6 | 982 | 0.36 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44274 | 0.59167 | 0.4 | 4.4 | 20.6 | 8 | 4 | 74.6 | 982 | -43.09 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PIND | LINE U PIN LINE D | 44274 | 0.59167 | 0.3 | 3.8 | 20.8 | 7 | 4 | 75.1 | 982 | -1.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB1 | LINE U PIN LINE B1 | 44274 | 0.57153 | 0.1 | 0.2 | 21.1 | 5 | 0 | 78.6 | 980 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB1 | LINE U PIN LINE B1 | 44274 | 0.57292 | 66.2 | 33.6 | 0.4 | 12 | 4 | 0 | 980 | -1.04 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB1 | LINE U PIN LINE B1 | 44274 | 0.58264 | 58 | 36.9 | 1.1 | 33 | 22 | 4 | 983 | -0.64 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB2 | LINE U PIN LINE B2 | 44274 | 0.57361 | 2.9 | 5.9 | 19.3 | 2 | 2 | 71.9 | 983 | -0.66 |  | 0 |  | Gas depletes when adjusted |  |  | No | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB2 | LINE U PIN LINE B2 | 44274 | 0.57431 | 51.3 | 29.5 | 3.6 | 68 | 44 | 15.6 | 983 | -15.24 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB2 | LINE U PIN LINE B2 | 44274 | 0.575 | 47.4 | 31.9 | 3.9 | 58 | 83 | 16.8 | 983 | -2.08 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB2 | LINE U PIN LINE B2 | 44274 | 0.58333 | 38.8 | 29.5 | 5.7 | 79 | 57 | 26 | 976 | -0.24 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB2 | LINE U PIN LINE B2 | 44274 | 0.58333 | 38.8 | 29.3 | 5.7 | 48 | 75 | 26.2 | 976 | -0.85 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB3 | LINE U PIN LINE B3 | 44274 | 0.57639 | 54.6 | 43.9 | 0.4 | 0 | 26 | 1.1 | 983 | -0.02 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB3 | LINE U PIN LINE B3 | 44274 | 0.57708 | 34.5 | 36.9 | 6.3 | 0 | 17 | 22.3 | 983 | -22.96 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB3 | LINE U PIN LINE B3 | 44274 | 0.58403 | 23.1 | 23.4 | 11.7 | 0 | 63 | 41.8 | 976 | -35.54 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0PNB3 | LINE U PIN LINE B3 | 44274 | 0.58472 | 22.3 | 22.4 | 12 | 0 | 44 | 43.3 | 976 | -3.96 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV1 | SCAVENGER | 44203 | 0.64653 | 65.3 | 35.8 | 0.8 | 17 | 4 | 0 | 967 | -144.97 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU0SCV1 | SCAVENGER | 44225 | 0.54514 | 64.2 | 35.6 | 0.9 | 57 | 0 | 0 | 952 | -153.89 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0SCV1 | SCAVENGER | 44253 | 0.59028 | 62.9 | 40.5 | 0.2 | 64 | 1516 | 0 | 987 | -185.12 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV1 | SCAVENGER | 44274 | 0.58542 | 61.3 | 38 | 0.3 | 0 | 24 | 0.4 | 980 | -178.62 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44203 | 0.64167 | 44.3 | 31.6 | 0.7 | 13 | 5 | 23.4 | 967 | -140.14 |  | 40 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU0SCV2 | SCAVENGER | 44225 | 0.53889 | 53.9 | 40.3 | 0.5 | 35 | 13 | 5.3 | 952 | -150.15 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44253 | 0.57639 | 70.3 | 26.6 | 0.8 | 37 | 5 | 2.3 | 987 | -177.91 |  | 30 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44253 | 0.57708 | 64.3 | 34.9 | 0.3 | 41 | 4 | 0.5 | 987 | -177.64 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44253 | 0.57778 | 62.5 | 36.6 | 0.4 | 40 | 4 | 0.5 | 987 | -182 |  | 50 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44274 | 0.59375 | 64.7 | 35.8 | 0.6 | 20 | 4 | 0 | 982 | -179.59 |  | 50 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV2 | SCAVENGER | 44274 | 0.59375 | 60.5 | 40.7 | 0.1 | 19 | 4 | 0 | 982 | -178.22 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV3 | SCAVENGER | 44203 | 0.63819 | 25.1 | 6.6 | 13.7 | 9 | 14 | 54.6 | 970 | -17.6 |  | 20 |  | Odour/migration control |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU0SCV3 | SCAVENGER | 44203 | 0.63889 | 25 | 15.5 | 12.1 | 34 | 16 | 47.4 | 970 | 0.16 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU0SCV3 | SCAVENGER | 44225 | 0.53611 | 56 | 24.7 | 3.6 | 18 | 24 | 15.7 | 952 | -0.57 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0SCV3 | SCAVENGER | 44225 | 0.53681 | 61.6 | 37.4 | 0.3 | 25 | 8 | 0.7 | 952 | -0.45 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0SCV3 | SCAVENGER | 44253 | 0.57847 | 61.5 | 36.5 | 0.4 | 46 | 3 | 1.6 | 987 | -4.36 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV3 | SCAVENGER | 44274 | 0.59514 | 60.7 | 38.2 | 0.3 | 19 | 3 | 0.8 | 980 | -0.36 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV3 | SCAVENGER | 44274 | 0.59514 | 60.1 | 39.3 | 0.4 | 20 | 3 | 0.2 | 980 | -2.95 |  | 20 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU0SCV4 | SCAVENGER | 44203 | 0.63681 | 67.5 | 39.5 | 0.7 | 74 | 950 | 0 | 967 | -140.94 |  | 100 |  | Condition good |  |  | No | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU0SCV4 | SCAVENGER | 44225 | 0.53403 | 66.3 | 40.2 | 0.7 | 59 | 690 | 0 | 952 | -151.84 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRU0SCV4 | SCAVENGER | 44253 | 0.58056 | 61.1 | 39 | 0.1 | 36 | 3 | 0 | 987 | -177.12 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | WET | NONE | 0.4 | SOUTH-WEST
TRU0SCV4 | SCAVENGER | 44274 | 0.59653 | 60.1 | 40.9 | 0.1 | 17 | 2 | 0 | 980 | -175.96 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | DRYING | NONE | 0.4 | SOUTH-WEST
TRU160MM | 160 MM LINE | 44203 | 0.65208 | 49.9 | 36.7 | 0.4 | 19 | 5 | 13 | 968 | -136.9 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | FROZEN | SNOW | 0.5 | NORTH-EAST
TRU160MM | 160 MM LINE | 44243 | 0.48819 | 50 | 36.2 | 1.2 | 76 | 1133 | 12.6 | 959 | -166.19 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRU160MM | 160 MM LINE | 44260 | 0.56736 | 62.7 | 41 | 0.3 | 71 | 1289 | 0 | 982 | -201.51 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRU355MM | Line U 355mm line | 44218 | 0.40556 | 57.7 | 38.1 | 0.8 | 89 | 1010 | 3.4 | 943 | -189.97 |  | 100 |  | Odour/migration control |  |  | No | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TRU355MM | Line U 355mm line | 44242 | 0.67014 | 45.5 | 33 | 1.7 | 69 | 662 | 19.8 | 967 | -173.46 |  | 100 |  | Odour/migration control |  |  | No | 19-24mph | SATURATED | SHOWERS | 1 | SOUTH-WEST
TRU355MM | Line U 355mm line | 44258 | 0.60069 | 51.7 | 36.7 | 0.8 | 52 | 549 | 10.8 | 976 | -182.05 |  | 100 |  | Odour/migration control |  |  | No | 8-11mph | DRYING | NONE | 0.2 | NORTH-EAST
TRUSCV1A | SCAVENGER 1A | 44225 | 0.54167 | 11.9 | 10.6 | 15.5 | 42 | 1 | 62 | 953 | 0.02 |  | 0 |  | Gas depletes when adjusted |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRUSCV1A | SCAVENGER 1A | 44225 | 0.54236 | 11.4 | 9.1 | 17.3 | 38 | 0 | 62.2 | 953 | -0.07 |  | 10 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRUSCV1A | SCAVENGER 1A | 44225 | 0.54306 | 10.7 | 8.8 | 17.6 | 35 | 0 | 62.9 | 953 | -0.23 |  | 0 |  | Gas depletes when adjusted |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRW160MM | LW 160 LINE | 44214 | 0.63819 | 66.5 | 42 | 0.7 | 27 | 108 | 0 | 972 | -136.98 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TRW160MM | LW 160 LINE | 44218 | 0.44236 | 55.8 | 38 | 1.2 | 38 | 69 | 5 | 945 | -176.76 |  | 100 |  | Condition good |  |  | N/A | 12-18mph | SATURATED | SHOWERS | 0.7 | SOUTH-WEST
TRW160MM | LW 160 LINE | 44230 | 0.54097 | 59.9 | 40 | 1.2 | 54 | 78 | 0 | 948 | -126.52 |  | 100 |  | Odour/migration control |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRW160MM | LW 160 LINE | 44263 | 0.63542 | 56.4 | 41.9 | 0.9 | 8 | 4 | 0.8 | 968 | -200.1 |  | 100 |  | Condition good |  |  | N/A | 8-11mph | DRYING | NONE | 0.2 | WEST
TRXLINE1 | 90MM LINE | 44228 | 0.62361 | 62.9 | 44.1 | 0.3 | 37 | 259 | 0 | 952 | -113.12 |  | 30 |  | Condition good |  |  | No | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST
TRXLINE1 | 90MM LINE | 44228 | 0.62431 | 62.7 | 44.6 | 0 | 36 | 364 | 0 | 952 | -117.23 |  | 40 |  | Condition good |  |  | N/A | 8-11mph | SATURATED | SHOWERS | 0.8 | SOUTH-WEST