## January
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-01-01
Weather: | Slight rain
Wind conditions: | Breezy
Air Temperature: | 6 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:30 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 997 | 0.5 | 1 | 8.8
BK BH 3 | 11:35 | 0.1 | 1.4 | 19.3 | 79.2 | 0 | 0 | 997 | -0.66 | 1 | 3.1
BK BH 4 | 11:37 | 0 | 0.8 | 19 | 80.2 | 0 | 0 | 997 | -0.23 | 1 | 5.1
BK BH 5 | 11:40 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 997 | -0.04 | 1 | 1.5
BK BH 6 | 11:43 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 997 | 0.51 | 1 | 1.5
BK BH 7 | 11:46 | 0 | 1 | 20 | 79 | 0 | 0 | 997 | 0.47 | 1 | 10
BK BH 8 | 11:49 | 30.1 | 1.2 | 19.5 | 49.2 | 0 | 0 | 997 | -0.41 | 32.2 | 3.6
BK BH 9 | 11:55 | 26.1 | 0.6 | 19.3 | 54 | 0 | 0 | 997 | 0.66 | 29.6 | 10.4
BK BH 10 | 12:00 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 997 | 0.83 | 1 | 3.9
BK BH 11 | 12:12 | 0 | 1.3 | 19.2 | 79.5 | 0 | 0 | 997 | -0.42 | 1 | 6.5
BK BH 12 | 12:16 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 997 | 0.37 | 1 | 6.6
BK BH 13 | 12:20 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 997 | -0.57 | 1 | 9.4
BK BH 14 | 12:23 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 997 | 0.42 | 1 | 3.5
BK BH 15 | 12:26 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 997 | 0.3 | 1 | 17.6
BK BH 16 | 12:29 | 0 | 1 | 19.2 | 79.8 | 0 | 0 | 997 | 0.71 | 1 | 11.4
BK BH 17 | 12:36 | 0.3 | 1 | 19.9 | 78.8 | 0 | 0 | 997 | 0.35 | 1 | 12.9
BK BH 18 | 11:03 | 0.2 | 1.2 | 19.6 | 79 | 0 | 0 | 997 | -0.32 | 6.8 | 21.2
BK BH 19 | 11:06 | 0 | 1.2 | 19.2 | 79.6 | 0 | 0 | 997 | 0.41 | 1 | 11.2
BK BH 20 | 11:09 | 0.1 | 0.9 | 19.3 | 79.7 | 0 | 0 | 997 | 0.39 | 1 | 10.7
BK BH 21 | 11:14 | 0.3 | 1.4 | 20 | 78.3 | 0 | 0 | 997 | 0.23 | 1 | 21.7
BK BH 23 | 11:19 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 997 | 0.6 | 1 | 7.3
BK BH 24 | 11:22 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 997 | -0.57 | 1 | 1.5
BK BH 25 | 11:26 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 997 | 0.53 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-01-08
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 8 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:38 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | 0.44 | 1 | 8.8
BK BH 3 | 11:43 | 0.3 | 1.1 | 19.3 | 79.3 | 0 | 0 | 997 | -0.63 | 1 | 3.1
BK BH 4 | 11:45 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 997 | -0.17 | 1 | 5.1
BK BH 5 | 11:47 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 997 | 0.23 | 1 | 1.5
BK BH 6 | 11:50 | 0 | 0.5 | 19.3 | 80.2 | 0 | 0 | 997 | 0.48 | 1 | 1.5
BK BH 7 | 11:54 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 997 | 0.44 | 1 | 10
BK BH 8 | 11:57 | 29.9 | 1 | 19.9 | 49.2 | 0 | 0 | 997 | -0.37 | 32.2 | 3.6
BK BH 9 | 12:03 | 26.3 | 0.4 | 19.5 | 53.8 | 0 | 0 | 997 | 0.68 | 29.6 | 10.4
BK BH 10 | 12:08 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.78 | 1 | 3.9
BK BH 11 | 12:20 | 0 | 1.3 | 19.4 | 79.3 | 0 | 0 | 997 | -0.23 | 1 | 6.5
BK BH 12 | 12:24 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 997 | 0.39 | 1 | 6.6
BK BH 13 | 12:28 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 997 | -0.74 | 1 | 9.4
BK BH 14 | 12:31 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 997 | 0.48 | 1 | 3.5
BK BH 15 | 12:34 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 997 | 0.26 | 1 | 17.6
BK BH 16 | 12:37 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 997 | 0.7 | 1 | 11.4
BK BH 17 | 12:44 | 0.2 | 0.9 | 20.1 | 78.8 | 0 | 0 | 997 | 0.49 | 1 | 12.9
BK BH 18 | 11:10 | 0.5 | 1.3 | 19.9 | 78.3 | 0 | 0 | 997 | -0.23 | 6.8 | 21.2
BK BH 19 | 11:14 | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 997 | 0.37 | 1 | 11.2
BK BH 20 | 11:17 | 0.3 | 1.2 | 19.5 | 79 | 0 | 0 | 997 | 0.21 | 1 | 10.7
BK BH 21 | 11:22 | 0.4 | 1.2 | 20.1 | 78.3 | 0 | 0 | 997 | 0.2 | 1 | 21.7
BK BH 23 | 11:27 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.67 | 1 | 7.3
BK BH 24 | 11:30 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 997 | -0.55 | 1 | 1.5
BK BH 25 | 11:34 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 997 | 0.67 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-01-15
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 8 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:15 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.44 | 1 | 8.8
BK BH 3 | 11:20 | 0.4 | 1.2 | 19.2 | 79.2 | 0 | 0 | 999 | -0.66 | 1 | 3.1
BK BH 4 | 11:22 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 999 | 0.23 | 1 | 5.1
BK BH 5 | 11:24 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 999 | 0.18 | 1 | 1.5
BK BH 6 | 11:27 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 999 | 0.65 | 1 | 1.5
BK BH 7 | 11:31 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | 0.45 | 1 | 10
BK BH 8 | 11:34 | 29.6 | 1.2 | 19.5 | 49.7 | 0 | 0 | 999 | -0.26 | 32.2 | 3.6
BK BH 9 | 11:40 | 26.8 | 0.6 | 19.7 | 52.9 | 0 | 0 | 999 | 0.55 | 29.6 | 10.4
BK BH 10 | 11:45 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 999 | 0.77 | 1 | 3.9
BK BH 11 | 11:57 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 999 | -0.04 | 1 | 6.5
BK BH 12 | 12:01 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.29 | 1 | 6.6
BK BH 13 | 12:05 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 999 | -0.67 | 1 | 9.4
BK BH 14 | 12:08 | 0 | 0.7 | 18.9 | 80.4 | 0 | 0 | 999 | 0.33 | 1 | 3.5
BK BH 15 | 12:11 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 999 | 0.07 | 1 | 17.6
BK BH 16 | 12:14 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 999 | 0.68 | 1 | 11.4
BK BH 17 | 12:21 | 0.3 | 1 | 19.5 | 79.2 | 0 | 0 | 999 | 0.47 | 1 | 12.9
BK BH 18 | 10:47 | 0.4 | 1.3 | 19.6 | 78.7 | 0 | 0 | 999 | -0.45 | 6.8 | 21.2
BK BH 19 | 10:51 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | 0.47 | 1 | 11.2
BK BH 20 | 10:54 | 0.2 | 1.1 | 20.1 | 78.6 | 0 | 0 | 999 | 0.03 | 1 | 10.7
BK BH 21 | 10:59 | 0.5 | 1.3 | 19.9 | 78.3 | 0 | 0 | 999 | 0.18 | 1 | 21.7
BK BH 23 | 11:04 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 999 | 0.43 | 1 | 7.3
BK BH 24 | 11:07 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | -0.5 | 1 | 1.5
BK BH 25 | 11:11 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 999 | 0.42 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-01-22
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 6 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:05 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1004 | 0.49 | 1 | 8.8
BK BH 3 | 11:10 | 0.2 | 1.4 | 19.4 | 79 | 0 | 0 | 1004 | -0.62 | 1 | 3.1
BK BH 4 | 11:12 | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 1004 | 0.06 | 1 | 5.1
BK BH 5 | 11:14 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1004 | 0.09 | 1 | 1.5
BK BH 6 | 11:17 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1004 | 0.75 | 1 | 1.5
BK BH 7 | 11:21 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1004 | 0.36 | 1 | 10
BK BH 8 | 11:24 | 29.5 | 1.1 | 19.9 | 49.5 | 0 | 0 | 1004 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:30 | 26.1 | 0.4 | 19.9 | 53.6 | 0 | 0 | 1004 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:35 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1004 | 0.69 | 1 | 3.9
BK BH 11 | 11:47 | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 1004 | -0.15 | 1 | 6.5
BK BH 12 | 11:51 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1004 | 0.24 | 1 | 6.6
BK BH 13 | 11:55 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 1004 | -0.63 | 1 | 9.4
BK BH 14 | 11:58 | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1004 | 0.21 | 1 | 3.5
BK BH 15 | 12:01 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1004 | 0.02 | 1 | 17.6
BK BH 16 | 12:04 | 0 | 1.2 | 19.2 | 79.6 | 0 | 0 | 1004 | 0.58 | 1 | 11.4
BK BH 17 | 12:11 | 0.4 | 1.2 | 20 | 78.4 | 0 | 0 | 1004 | 0.77 | 1 | 12.9
BK BH 18 | 10:37 | 0.2 | 1 | 19.9 | 78.9 | 0 | 0 | 1004 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:41 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 1004 | 0.38 | 1 | 11.2
BK BH 20 | 10:44 | 0.3 | 1.3 | 19.8 | 78.6 | 0 | 0 | 1004 | -0.25 | 1 | 10.7
BK BH 21 | 10:49 | 0.4 | 1 | 20.1 | 78.5 | 0 | 0 | 1004 | 0.14 | 1 | 21.7
BK BH 23 | 10:54 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1004 | 0.75 | 1 | 7.3
BK BH 24 | 10:57 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1004 | -0.63 | 1 | 1.5
BK BH 25 | 11:01 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1004 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-01-29
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 9 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:00 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1007 | 0.39 | 1 | 8.8
BK BH 3 | 11:05 | 0.3 | 1.6 | 19.2 | 78.9 | 0 | 0 | 1007 | -0.55 | 1 | 3.1
BK BH 4 | 11:07 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1007 | -0.02 | 1 | 5.1
BK BH 5 | 11:10 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 1007 | -0.4 | 1 | 1.5
BK BH 6 | 11:13 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1007 | 0.59 | 1 | 1.5
BK BH 7 | 11:16 | 0 | 0.7 | 19.4 | 79.9 | 0 | 0 | 1007 | 0.31 | 1 | 10
BK BH 8 | 11:19 | 29.2 | 0.8 | 20.1 | 49.9 | 0 | 0 | 1007 | -0.37 | 32.2 | 3.6
BK BH 9 | 11:25 | 26.4 | 0.6 | 19.8 | 53.2 | 0 | 0 | 1007 | 0.61 | 29.6 | 10.4
BK BH 10 | 11:30 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1007 | 0.8 | 1 | 3.9
BK BH 11 | 11:42 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1007 | -0.11 | 1 | 6.5
BK BH 12 | 11:46 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 1007 | 0.4 | 1 | 6.6
BK BH 13 | 11:50 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 1007 | -0.8 | 1 | 9.4
BK BH 14 | 11:53 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1007 | 0.43 | 1 | 3.5
BK BH 15 | 11:56 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1007 | 0.15 | 1 | 17.6
BK BH 16 | 11:59 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1007 | 0.61 | 1 | 11.4
BK BH 17 | 12:06 | 0.3 | 1 | 19.8 | 78.9 | 0 | 0 | 1007 | 0.57 | 1 | 12.9
BK BH 18 | 10:33 | 0.6 | 0.9 | 20.1 | 78.4 | 0 | 0 | 1007 | -0.35 | 6.8 | 21.2
BK BH 19 | 10:36 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 1007 | 0.31 | 1 | 11.2
BK BH 20 | 10:39 | 0.2 | 0.9 | 19.3 | 79.6 | 0 | 0 | 1007 | 0.15 | 1 | 10.7
BK BH 21 | 10:44 | 0.5 | 1.1 | 19.3 | 79.1 | 0 | 0 | 1007 | 0.26 | 1 | 21.7
BK BH 23 | 10:49 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1007 | 0.59 | 1 | 7.3
BK BH 24 | 10:52 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1007 | -0.62 | 1 | 1.5
BK BH 25 | 10:56 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1007 | 0.58 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-01-06
Weather: |  | dry + overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 9 | oC
Instrument: |  | GA 2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2016-03-26
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:30 | 47.9 | 33.2 | 0.6 | 18.3 | 12 | 7 | 997 | 175 |  | Egine running
GV1 |  | 21.8 | 26.5 | 2.6 | 49.1 | 6 | 0 | 997 |  |  | OFF
GV3 |  | 58.9 | 33.2 | 0.2 | 7.7 | 6 | 12 | 997 | -25.23 |  | Open Full
GV4 |  | 40.1 | 35.6 | 0.2 | 24.1 | 9 | 9 | 997 | -9.23 |  | Cracked Open
GV6 |  | 44.3 | 32.9 | 0.4 | 22.4 | 6 | 0 | 997 | -7.23 |  | Cracked Open
GV7 |  | 26.9 | 29.9 | 3 | 40.2 | 8 | 0 | 997 | -1.27 |  | Off Low Gas high o2
GV8 |  | 35.6 | 23.6 | 2.1 | 38.7 | 9 | 0 | 997 | -1.36 |  | Off Low Gas high o3
GV9 |  | 45.2 | 38.2 | 0 | 16.6 | 8 | 0 | 997 | -26.87 |  | Open Full
GV10 |  | 37.6 | 19.9 | 2 | 40.5 | 6 | 0 | 997 | -1.56 |  | Off
GV11 |  | 29.9 | 24.5 | 0.3 | 45.3 | 0 | 0 | 997 | -1.39 |  | Off
GV12+R3 Manifold |  | 50.2 | 35.4 | 0.2 | 14.2 | 10 | 22 | 997 | -25.69 |  | Open Full
GV12 |  | 48.6 | 38.2 | 0.6 | 12.6 | 4 | 0 | 997 | -26.74 |  | Open Full
R3 |  | 52.3 | 36 | 0.2 | 11.5 | 9 | 0 | 997 | -25.39 |  | Open Full
GV13 |  | 51.2 | 33.4 | 0.9 | 14.5 | 0 | 0 | 997 | -27.84 |  | Open Full
GV14 |  | 42.3 | 35.9 | 0.4 | 21.4 | 8 | 37 | 997 | -26.39 |  | Open Full
GV15 |  | 55.3 | 37.6 | 0.6 | 6.5 | 14 | 32 | 997 | -25.48 |  | Open Full
GV16 |  | 27.9 | 35.6 | 0.5 | 36 | 9 | 9 | 997 | -9.39 | -1.27 | Reg closed Gas dropped
GV17+LC4 Manifold |  | 33.6 | 31.8 | 4 | 30.6 | 6 | 6 | 997 | -1.28 |  | Off at Manifold Gas drops quick.
GV17 |  | 36.9 | 35.6 | 4.2 | 23.3 | 3 | 9 | 997 | -1.23 |  | Open Full at Well
LC4 |  | 32.7 | 28.9 | 3.7 | 34.7 | 4 | 11 | 997 | -1.19 |  | Open Full at well
GV18 |  | 56.3 | 38.7 | 0.5 | 4.5 | 17 | 52 | 997 | -26.39 |  | Open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 31.2 | 26.9 | 2.3 | 39.6 | 10 | 7 | 997 | -1.39 |  | Off gas drops off quick.
GV23 |  | 58.9 | 39.9 | 0.4 | 0.8 | 8 | 46 | 997 | -26.21 |  | Open Full
GV24 |  | 56.4 | 38.9 | 0.5 | 4.2 | 6 | 6 | 997 | -25.39 |  | Open Full
GV25 |  | 51.3 | 35.7 | 0.2 | 12.8 | 8 | 1 | 997 | -26.79 |  | Open Full
GV26 + 27 Manifold |  | 54.6 | 38.6 | 0.6 | 6.2 | 10 | 21 | 997 | -25.6 |  | Open Full
GV28+ 29 Manifold |  | 51.9 | 37.9 | 0.3 | 9.9 | 9 | 17 | 997 | -24.99 |  | Open Full
GV26 |  | 51.2 | 39.8 | 0.2 | 8.8 | 8 | 0 | 997 | -25.23 |  | Open Full
GV27 |  | 55.9 | 42.1 | 0.4 | 1.6 | 12 | 30 | 997 | -25.37 |  | Open Full
GV28 |  | 48.9 | 35.9 | 0.5 | 14.7 | 5 | 5 | 997 | -26.17 |  | Open Full
GV29 |  | 52.3 | 35.9 | 0.3 | 11.5 | 9 | 26 | 997 | -25.55 |  | Open Full
GVA |  | 24.9 | 19.8 | 11.3 | 44 | 5 | 4 | 997 | -1.39 |  | Off Low gas
B+C Manifold |  | 43.6 | 37 | 0.6 | 18.8 | 10 | 0 | 997 | -26.39 |  | Open Full
GV B |  | 42.6 | 39.2 | 0.8 | 17.4 | 10 | 9 | 997 | -27.48 |  | Open Full
GV C |  | 46.9 | 36.9 | 0.5 | 15.7 | 5 | 6 | 997 | -25.69 |  | Open Full
GV30 |  | 43.3 | 29.6 | 1.2 | 25.9 | 8 | 4 | 997 | -6.45 |  | Cracked Open
GV31 |  | 45.6 | 30.1 | 1.3 | 23 | 6 | 8 | 997 | -7.23 |  | Cracked Open
GV32 |  | 46.3 | 26.4 | 1 | 26.3 | 5 | 9 | 997 | -9.39 |  | Cracked Open
GV33 |  | 48.9 | 29.9 | 1.2 | 20 | 6 | 10 | 997 | -4.68 |  | Cracked Open
GV34 |  | 47.6 | 25.6 | 1.4 | 25.4 | 11 | 6 | 997 | -5.69 |  | Cracked Open
GV 35 (New Well) |  | 45.6 | 32.9 | 0.6 | 20.9 | 6 | 2 | 997 | -25.05 |  | Open Full
GV 36 (New Well) |  | 18.9 | 21.7 | 3.8 | 55.6 | 10 | 9 | 997 | -1.23 |  | OFF low gas.
GV 37 (New Well) |  | 25.6 | 22.6 | 0.6 | 51.2 | 9 | 0 | 997 | -1.86 |  | OFF low gas.
GV 38 (New Well) |  | 43.3 | 30.8 | 0.3 | 25.6 | 5 | 3 | 997 | -25.69 |  | Open Full
GV 39 (New Well) |  | 42.3 | 32.9 | 0.5 | 24.3 | 8 | 0 | 997 | -24.63 |  | Open Full
GV 40 (New Well) |  | 42.9 | 29.9 | 0.4 | 26.8 | 10 | 0 | 997 | -25.89 |  | Open Full
GV 41 (New Well) |  | 41.2 | 32.5 | 1.4 | 24.9 | 10 | 0 | 997 | -7.31 |  | Cracked Open
GV 42 (New Well) |  | 29.6 | 26.9 | 0.6 | 42.9 | 4 | 2 | 997 | -1.22 |  | Off Low Gas
GV 43 (New Well) |  | 37.9 | 29.9 | 0.3 | 31.9 | 7 | 3 | 997 | -7.69 |  | Cracked Open
GV 44 (New Well) |  | 30.2 | 24.5 | 0.2 | 45.1 | 14 | 4 | 997 | -3.96 |  | Off Low gas
GV 45 (New Well) |  | 44.9 | 29.9 | 0.3 | 24.9 | 7 | 5 | 997 | -7.71 |  | Cracked Open
GV 46 (New Well) |  | 46.4 | 38.9 | 0.4 | 14.3 | 10 | 3 | 997 | -25.63 |  | Open Full
GV 47 (New Well) |  | 43.9 | 34.5 | 0.6 | 21 | 6 | 0 | 997 | -6.32 |  | Cracked Opem
GV 48 (New Well) |  | 57.9 | 41.3 | 0.5 | 0.3 | 6 | 27 | 997 | -26.09 |  | Open Full
GV 49 (New Well) |  | 31.2 | 35.6 | 3 | 30.2 | 8 | 15 | 997 | -7.52 | -1.06 | Reg turned off
LC1B |  | 29.9 | 34.2 | 3.1 | 32.8 | 6 | 13 | 997 | -1.2 |  | OFF
LC2R? |  | 46.9 | 33.8 | 1.2 | 18.1 | 10 | 5 | 997 | -26.32 |  | Open Full
GV 2.1 |  | 47.8 | 36.6 | 0.9 | 14.7 | 9 | 2 | 997 | -25.48 |  | Open Full
GV 2.2+ LC2B MAN |  | 45.8 | 33.3 | 1.2 | 19.7 | 7 | 8 | 997 | -6.83 |  | Cracked Open at Manifold
GV 2.2 |  | 46.6 | 34.6 | 1.3 | 17.5 | 3 | 6 | 997 | -6.53 |  | Cracked Open
LC2B |  | 44.7 | 35.6 | 1 | 18.7 | 5 | 12 | 997 | -5.23 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 39.9 | 33.6 | 1.4 | 25.1 | 6 | 5 | 997 | -1.06 |  | Off
LC3.1 |  | 40.1 | 34.9 | 1.4 | 23.6 | 10 | 9 | 997 | -1.09 |  | Open At well
LC3 |  | 45.6 | 32.6 | 1.4 | 20.4 | 8 | 9 | 997 | -1.01 |  | OFF
LC4B |  | 43.9 | 34.5 | 1.2 | 20.4 | 6 | 14 | 997 | -5.69 |  | Cracked Open
R1 + R1B Manifold |  | 46.8 | 32.6 | 0.6 | 20 | 4 | 19 | 997 | -26.96 |  | Open Full
R1 |  | 44.6 | 30.6 | 1.1 | 23.7 | 3 | 10 | 997 | -6.97 |  | Cracked Open
R1B |  | 50.2 | 33.9 | 0.2 | 15.7 | 5 | 19 | 997 | -25.03 |  | Open Full
R2B |  | 51.2 | 34.9 | 0.3 | 13.6 | 7 | 21 | 997 | -25.21 |  | Open Full
R4B |  | 49.8 | 32.6 | 0.4 | 17.2 | 5 | 19 | 997 | -26.38 |  | Open Full
R6B |  | 46.6 | 31.2 | 0.2 | 22 | 10 | 9 | 997 | -24.98 |  | Open Full
LC5 |  | 48.3 | 33.6 | 0.3 | 17.8 | 6 | 4 | 997 | -1.56 |  | Left Off ( Gas drops quick)
LC6 |  | 46.5 | 31.6 | 1.9 | 20 | 9 | 10 | 997 | -1.09 |  | Left Off ( Gas drops quick)
LC6B |  | 50.8 | 30.9 | 1.9 | 16.4 | 7 | 19 | 997 | -26.79 |  | Open Full
PW1 |  | 0.5 | 0 | 16.9 | 82.6 | 3 | 8 | 997 | -1.36 |  | Left Off
PW2 |  | 29.9 | 19.6 | 2.9 | 47.6 | 11 | 7 | 997 | -1.48 |  | Left Off
PW3 |  | 28.7 | 20 | 6.2 | 45.1 | 9 | 10 | 997 | -1.32 |  | Left Off
PW4 |  | 44.6 | 30.2 | 0.7 | 24.5 | 4 | 15 | 997 | -4.59 |  | Cracked Open
PW5 |  | 25.6 | 20.3 | 0.9 | 53.2 | 8 | 14 | 997 | -1.02 |  | Left Off
PW6 |  | 24.1 | 22.1 | 1.7 | 52.1 | 9 | 16 | 997 | -1.29 |  | Left Off
Flare | 13:45 | 48.5 | 34.2 | 0.5 | 16.8 | 12 | 13 | 997 | 178 |  | Engine running 550 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## February
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-02-05
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 8 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:15 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 996 | 0.49 | 1 | 8.8
BK BH 3 | 11:20 | 0.2 | 1.4 | 19.5 | 78.9 | 0 | 0 | 996 | -0.62 | 1 | 3.1
BK BH 4 | 11:22 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 996 | 0.02 | 1 | 5.1
BK BH 5 | 11:24 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 996 | 0 | 1 | 1.5
BK BH 6 | 11:27 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 996 | 0.75 | 1 | 1.5
BK BH 7 | 11:31 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 996 | 0.36 | 1 | 10
BK BH 8 | 11:34 | 29.5 | 1 | 20 | 49.5 | 0 | 0 | 996 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:40 | 26.8 | 0.9 | 19.5 | 52.8 | 0 | 0 | 996 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:45 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 996 | 0.69 | 1 | 3.9
BK BH 11 | 11:57 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 996 | -0.15 | 1 | 6.5
BK BH 12 | 12:01 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 996 | 0.24 | 1 | 6.6
BK BH 13 | 12:05 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 996 | -0.63 | 1 | 9.4
BK BH 14 | 12:08 | 0 | 1.3 | 19.3 | 79.4 | 0 | 0 | 996 | 0.21 | 1 | 3.5
BK BH 15 | 12:11 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 996 | 0.02 | 1 | 17.6
BK BH 16 | 12:14 | 0 | 1 | 19.1 | 79.9 | 0 | 0 | 996 | 0.58 | 1 | 11.4
BK BH 17 | 12:21 | 0.2 | 1.3 | 20.1 | 78.4 | 0 | 0 | 996 | 0.77 | 1 | 12.9
BK BH 18 | 10:47 | 0.4 | 1.7 | 20 | 77.9 | 0 | 0 | 996 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:51 | 0 | 1.2 | 19.1 | 79.7 | 0 | 0 | 996 | 0.38 | 1 | 11.2
BK BH 20 | 10:54 | 0.4 | 0.5 | 19.1 | 80 | 0 | 0 | 996 | -0.25 | 1 | 10.7
BK BH 21 | 10:59 | 0.4 | 1.3 | 19.9 | 78.4 | 0 | 0 | 996 | 0.14 | 1 | 21.7
BK BH 23 | 11:04 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 996 | 0.75 | 1 | 7.3
BK BH 24 | 11:07 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 996 | -0.63 | 1 | 1.5
BK BH 25 | 11:11 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 996 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-02-12
Weather: | Calm
Wind conditions: | Breezy
Air Temperature: | 9 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:05 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1000 | 0.44 | 1 | 8.8
BK BH 3 | 11:10 | 0.4 | 1.5 | 19.8 | 78.3 | 0 | 0 | 1000 | -0.66 | 1 | 3.1
BK BH 4 | 11:12 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1000 | 0.21 | 1 | 5.1
BK BH 5 | 11:14 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1000 | -0.01 | 1 | 1.5
BK BH 6 | 11:17 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1000 | 0.65 | 1 | 1.5
BK BH 7 | 11:21 | 0 | 1 | 19.2 | 79.8 | 0 | 0 | 1000 | 0.45 | 1 | 10
BK BH 8 | 11:24 | 30 | 1.4 | 19.5 | 49.1 | 0 | 0 | 1000 | -0.26 | 32.2 | 3.6
BK BH 9 | 11:30 | 27.1 | 1.2 | 19.5 | 52.2 | 0 | 0 | 1000 | 0.55 | 29.6 | 10.4
BK BH 10 | 11:35 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 1000 | 0.77 | 1 | 3.9
BK BH 11 | 11:47 | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1000 | -0.04 | 1 | 6.5
BK BH 12 | 11:51 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 1000 | 0.29 | 1 | 6.6
BK BH 13 | 11:55 | 0 | 1 | 19 | 80 | 0 | 0 | 1000 | -0.67 | 1 | 9.4
BK BH 14 | 11:58 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1000 | 0.33 | 1 | 3.5
BK BH 15 | 12:01 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1000 | 0.07 | 1 | 17.6
BK BH 16 | 12:04 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1000 | 0.68 | 1 | 11.4
BK BH 17 | 12:11 | 0.4 | 3.2 | 19.9 | 76.5 | 0 | 0 | 1000 | 0.47 | 1 | 12.9
BK BH 18 | 10:37 | 0.4 | 2 | 20.1 | 77.5 | 0 | 0 | 1000 | -0.45 | 6.8 | 21.2
BK BH 19 | 10:41 | 0 | 1 | 19 | 80 | 0 | 0 | 1000 | 0.47 | 1 | 11.2
BK BH 20 | 10:44 | 0.3 | 0.9 | 19.4 | 79.4 | 0 | 0 | 1000 | 0.03 | 1 | 10.7
BK BH 21 | 10:49 | 0.5 | 1 | 19.3 | 79.2 | 0 | 0 | 1000 | 0.18 | 1 | 21.7
BK BH 23 | 10:54 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 1000 | 0.43 | 1 | 7.3
BK BH 24 | 10:57 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1000 | -0.5 | 1 | 1.5
BK BH 25 | 11:01 | 0 | 1.1 | 19.3 | 79.6 | 0 | 0 | 1000 | 0.42 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-02-19
Weather: | dry
Wind conditions: | calm
Air Temperature: | 7 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 994 | -0.5 | 1 | 8.8
BK BH 3 | 10:08 | 0.3 | 1.4 | 19.8 | 78.5 | 0 | 0 | 994 | 0.71 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 994 | 0.62 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 0.7 | 19.1 | 80.2 | 0 | 0 | 994 | 0.54 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 994 | 0.63 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 1.3 | 19.3 | 79.4 | 0 | 0 | 994 | -0.15 | 1 | 10
BK BH 8 | 10:22 | 29.6 | 1.1 | 19.7 | 49.6 | 0 | 0 | 994 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:28 | 28.1 | 1.3 | 19.9 | 50.7 | 0 | 0 | 994 | 0.25 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 994 | 0.75 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 994 | 0.15 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 1.1 | 19.3 | 79.6 | 0 | 0 | 994 | -0.87 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 994 | 0.36 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.7 | 20.1 | 78.2 | 0 | 0 | 994 | 0.46 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 994 | -0.14 | 1 | 17.6
BK BH 16 | 11:02 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 994 | 0.69 | 1 | 11.4
BK BH 17 | 11:09 | 0.3 | 3.3 | 19.9 | 76.5 | 0 | 0 | 994 | 0.36 | 1 | 12.9
BK BH 18 | 9:35 | 0.2 | 2.1 | 20.1 | 77.6 | 0 | 0 | 994 | -0.47 | 6.8 | 21.2
BK BH 19 | 9:39 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 994 | -0.15 | 1 | 11.2
BK BH 20 | 9:42 | 0.4 | 0.9 | 19.8 | 78.9 | 0 | 0 | 994 | 0.63 | 1 | 10.7
BK BH 21 | 9:47 | 0.4 | 1.3 | 19.6 | 78.7 | 0 | 0 | 994 | -0.25 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 1.2 | 19.3 | 79.5 | 0 | 0 | 994 | 0.71 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 994 | 0.36 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 994 | -0.17 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-02-26
Weather: | dry
Wind conditions: | calm
Air Temperature: | 10 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-03-26
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:38 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1001 | -0.62 | 1 | 8.8
BK BH 3 | 11:43 | 0.4 | 1.2 | 20 | 78.4 | 0 | 0 | 1001 | 0.35 | 1 | 3.1
BK BH 4 | 11:45 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1001 | 0.21 | 1 | 5.1
BK BH 5 | 11:47 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 1001 | 0.36 | 1 | 1.5
BK BH 6 | 11:50 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1001 | -0.11 | 1 | 1.5
BK BH 7 | 11:54 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1001 | 0.42 | 1 | 10
BK BH 8 | 11:57 | 29.4 | 1.2 | 19.9 | 49.5 | 0 | 0 | 1001 | 0.75 | 32.2 | 3.6
BK BH 9 | 12:03 | 27.8 | 1.1 | 19.8 | 51.3 | 0 | 0 | 1001 | -0.62 | 29.6 | 10.4
BK BH 10 | 12:08 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1001 | 0.31 | 1 | 3.9
BK BH 11 | 12:20 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 1001 | 0.25 | 1 | 6.5
BK BH 12 | 12:24 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1001 | -0.98 | 1 | 6.6
BK BH 13 | 12:28 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1001 | 0.62 | 1 | 9.4
BK BH 14 | 12:31 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1001 | 0.34 | 1 | 3.5
BK BH 15 | 12:34 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 1001 | -0.11 | 1 | 17.6
BK BH 16 | 12:37 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1001 | 0.24 | 1 | 11.4
BK BH 17 | 12:44 | 0.4 | 3.2 | 19.5 | 76.9 | 0 | 0 | 1001 | 0.15 | 1 | 12.9
BK BH 18 | 11:10 | 0.1 | 2 | 19.7 | 78.2 | 0 | 0 | 1001 | 0.63 | 6.8 | 21.2
BK BH 19 | 11:14 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1001 | -0.75 | 1 | 11.2
BK BH 20 | 11:17 | 0.3 | 1 | 20 | 78.7 | 0 | 0 | 1001 | 0.63 | 1 | 10.7
BK BH 21 | 11:22 | 0.2 | 1.4 | 20.1 | 78.3 | 0 | 0 | 1001 | 0.28 | 1 | 21.7
BK BH 23 | 11:27 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1001 | -0.78 | 1 | 7.3
BK BH 24 | 11:30 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 1001 | 0.12 | 1 | 1.5
BK BH 25 | 11:34 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1001 | 0.35 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-02-10
Weather: |  | dry + overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 8 | oC
Instrument: |  | GA 2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2016-03-26
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:20 | 49.9 | 34.6 | 0.5 | 15 | 7 | 8 | 1003 | 180 |  | Egine running
GV1 |  | 22.5 | 26.9 | 3 | 47.6 | 7 | 4 | 1003 |  |  | OFF
GV3 |  | 57.6 | 35.9 | 0.3 | 6.2 | 7 | 9 | 1003 | -26.56 |  | Open Full
GV4 |  | 43 | 34.9 | 0.5 | 21.6 | 8 | 6 | 1003 | -8.97 |  | Cracked Open
GV6 |  | 45.5 | 33.6 | 0.4 | 20.5 | 9 | 8 | 1003 | -6.96 |  | Cracked Open
GV7 |  | 30 | 27.4 | 2.2 | 40.4 | 6 | 5 | 1003 | -1.04 |  | Off Low Gas high o2
GV8 |  | 39.9 | 26.9 | 1.8 | 31.4 | 8 | 3 | 1003 | -1.39 |  | Off Low Gas high o3
GV9 |  | 46.9 | 33.5 | 0 | 19.6 | 14 | 2 | 1003 | -26.01 |  | Open Full
GV10 |  | 39.9 | 21.7 | 1.8 | 36.6 | 4 | 0 | 1003 | -1.06 |  | Off
GV11 |  | 32.5 | 26.9 | 0.5 | 40.1 | 8 | 0 | 1003 | -1.48 |  | Off
GV12+R3 Manifold |  | 50.2 | 33.2 | 0.1 | 16.5 | 5 | 1 | 1003 | -26.93 |  | Open Full
GV12 |  | 51.1 | 35.1 | 0.2 | 13.6 | 2 | 4 | 1003 | -27.12 |  | Open Full
R3 |  | 49.6 | 31.6 | 0 | 18.8 | 1 | 5 | 1003 | -26.47 |  | Open Full
GV13 |  | 50 | 35.4 | 0.6 | 14 | 4 | 6 | 1003 | -26.31 |  | Open Full
GV14 |  | 48.9 | 38.7 | 0.8 | 11.6 | 7 | 8 | 1003 | -26.98 |  | Open Full
GV15 |  | 52.4 | 35.6 | 0.5 | 11.5 | 9 | 7 | 1003 | -26.51 |  | Open Full
GV16 |  | 39.9 | 30.4 | 2.3 | 27.4 | 8 | 4 | 1003 | -1.2 |  | Left OFF
GV17+LC4 Manifold |  | 35.2 | 32.6 | 3.8 | 28.4 | 3 | 5 | 1003 | -1 |  | Off at Manifold Gas drops quick.
GV17 |  | 37.2 | 34.8 | 4.2 | 23.8 | 6 | 8 | 1003 | -0.99 |  | Open Full at Well
LC4 |  | 33.6 | 29.9 | 3.7 | 32.8 | 5 | 5 | 1003 | -1.06 |  | Open Full at well
GV18 |  | 51.2 | 36.8 | 0.4 | 11.6 | 12 | 2 | 1003 | -26.78 |  | Open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 34.5 | 28.9 | 2.6 | 34 | 7 | 9 | 1003 | -1.45 |  | Off gas drops off quick.
GV23 |  | 55.6 | 36.8 | 0.2 | 7.4 | 4 | 26 | 1003 | -26.96 |  | Open Full
GV24 |  | 54.4 | 37.2 | 0.3 | 8.1 | 5 | 8 | 1003 | -26.45 |  | Open Full
GV25 |  | 53.9 | 38 | 0.4 | 7.7 | 6 | 2 | 1003 | -26.66 |  | Open Full
GV26 + 27 Manifold |  | 50.1 | 35.4 | 0.9 | 13.6 | 3 | 3 | 1003 | -26.14 |  | Open Full
GV28+ 29 Manifold |  | 49.9 | 31.1 | 0.6 | 18.4 | 2 | 9 | 1003 | -26.68 |  | Open Full
GV26 |  | 51 | 37.9 | 0.4 | 10.7 | 5 | 6 | 1003 | -25.99 |  | Open Full
GV27 |  | 53.9 | 36.7 | 0.5 | 8.9 | 7 | 8 | 1003 | -26.35 |  | Open Full
GV28 |  | 51.1 | 38.4 | 0.6 | 9.9 | 8 | 6 | 1003 | -26.98 |  | Open Full
GV29 |  | 50.3 | 36.9 | 0.4 | 12.4 | 4 | 6 | 1003 | -26.41 |  | Open Full
GVA |  | 26.9 | 21.3 | 9.9 | 41.9 | 8 | 3 | 1003 | -1.03 |  | Off Low gas
B+C Manifold |  | 46.6 | 35.4 | 0.9 | 17.1 | 5 | 19 | 1003 | -26.58 |  | Open Full
GV B |  | 47.1 | 38.9 | 0.8 | 13.2 | 10 | 6 | 1003 | -27.48 |  | Open Full
GV C |  | 46.9 | 37.8 | 0.6 | 14.7 | 0 | 3 | 1003 | -26.99 |  | Open Full
GV30 |  | 45 | 32.9 | 1.2 | 20.9 | 0 | 8 | 1003 | -8.96 |  | Cracked Open
GV31 |  | 46.6 | 32.6 | 1.1 | 19.7 | 0 | 9 | 1003 | -7.47 |  | Cracked Open
GV32 |  | 45.1 | 31.4 | 1.2 | 22.3 | 5 | 8 | 1003 | -5.69 |  | Cracked Open
GV33 |  | 46.3 | 33.2 | 1.2 | 19.3 | 9 | 45 | 1003 | -9.31 |  | Cracked Open
GV34 |  | 45.2 | 29.9 | 1.4 | 23.5 | 9 | 5 | 1003 | -8.93 |  | Cracked Open
GV 35 (New Well) |  | 46.9 | 33.5 | 0.5 | 19.1 | 6 | 6 | 1003 | -26.47 |  | Open Full
GV 36 (New Well) |  | 19.9 | 24.5 | 3.5 | 52.1 | 9 | 9 | 1003 | -0.21 |  | OFF low gas.
GV 37 (New Well) |  | 30.2 | 24.5 | 0.9 | 44.4 | 8 | 8 | 1003 | -0.89 |  | OFF low gas.
GV 38 (New Well) |  | 45.4 | 31.8 | 0.2 | 22.6 | 7 | 8 | 1003 | -26.96 |  | Open Full
GV 39 (New Well) |  | 46.3 | 33.6 | 0.3 | 19.8 | 5 | 0 | 1003 | -26.47 |  | Open Full
GV 40 (New Well) |  | 44.5 | 31.5 | 0.4 | 23.6 | 3 | 0 | 1003 | -26.89 |  | Open Full
GV 41 (New Well) |  | 42 | 35.2 | 1 | 21.8 | 8 | 0 | 1003 | -8 |  | Cracked Open
GV 42 (New Well) |  | 35.6 | 29.9 | 0.9 | 33.6 | 9 | 2 | 1003 | -1.56 |  | Off Low Gas
GV 43 (New Well) |  | 40.1 | 32.4 | 1 | 26.5 | 11 | 5 | 1003 | -8.04 |  | Cracked Open
GV 44 (New Well) |  | 36.4 | 29.8 | 0.5 | 33.3 | 14 | 6 | 1003 | -2.05 |  | Off Low gas
GV 45 (New Well) |  | 44 | 28.9 | 0.6 | 26.5 | 13 | 8 | 1003 | -8.01 |  | Cracked Open
GV 46 (New Well) |  | 48.9 | 40 | 0.3 | 10.8 | 12 | 7 | 1003 | -26.06 |  | Open Full
GV 47 (New Well) |  | 42.1 | 33.6 | 1.1 | 23.2 | 8 | 0 | 1003 | -7.89 |  | Cracked Opem
GV 48 (New Well) |  | 58.2 | 40 | 0.4 | 1.4 | 5 | 27 | 1003 | -26.48 |  | Open Full
GV 49 (New Well) |  | 32.5 | 28.9 | 2.8 | 35.8 | 3 | 6 | 1003 | -1.23 |  | Left OFF
LC1B |  | 35.2 | 33.2 | 3.2 | 28.4 | 2 | 9 | 1003 | -0.96 |  | OFF
LC2R? |  | 47.2 | 34.5 | 1 | 17.3 | 6 | 8 | 1003 | -26.58 |  | Open Full
GV 2.1 |  | 46.9 | 37.8 | 0.6 | 14.7 | 8 | 13 | 1003 | -26.03 |  | Open Full
GV 2.2+ LC2B MAN |  | 46 | 32.5 | 1 | 20.5 | 7 | 9 | 1003 | -7.58 |  | Cracked Open at Manifold
GV 2.2 |  | 46.9 | 34 | 0.8 | 18.3 | 6 | 3 | 1003 | -7.23 |  | Cracked Open
LC2B |  | 44.8 | 30.8 | 1.2 | 23.2 | 8 | 6 | 1003 | -7.89 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 40.2 | 32.6 | 1.5 | 25.7 | 5 | 5 | 1003 | -1.23 |  | Off
LC3.1 |  | 40.2 | 32.6 | 1.5 | 25.7 | 2 | 8 | 1003 | -1 |  | Open At well
LC3 |  | 39.9 | 31.5 | 2.9 | 25.7 | 1 | 9 | 1003 | -1 |  | OFF
LC4B |  | 45.9 | 33.6 | 1.1 | 19.4 | 8 | 7 | 1003 | -1.23 |  | Cracked Open
R1 + R1B Manifold |  | 48.9 | 33 | 0.7 | 17.4 | 4 | 4 | 1003 | -26.89 |  | Open Full
R1 |  | 45.9 | 30.6 | 1 | 22.5 | 7 | 4 | 1003 | -8.39 |  | Cracked Open
R1B |  | 49.9 | 35 | 0.4 | 14.7 | 5 | 2 | 1003 | -26.74 |  | Open Full
R2B |  | 50 | 34.1 | 0.2 | 15.7 | 4 | 3 | 1003 | -26.59 |  | Open Full
R4B |  | 49.8 | 33.8 | 0.3 | 16.1 | 4 | 19 | 1003 | -26.31 |  | Open Full
R6B |  | 46.8 | 32.6 | 0.4 | 20.2 | 4 | 9 | 1003 | -26.03 |  | Open Full
LC5 |  | 47.6 | 32.4 | 2.6 | 17.4 | 8 | 5 | 1003 | -1.25 |  | Left Off ( Gas drops quick)
LC6 |  | 50.2 | 33.5 | 3.9 | 12.4 | 9 | 3 | 1003 | -1.87 |  | Left Off ( Gas drops quick)
LC6B |  | 51.2 | 33.5 | 0.9 | 14.4 | 6 | 23 | 1003 | -26.09 |  | Open Full
PW1 |  | 0.9 | 0 | 15.9 | 83.2 | 6 | 11 | 1003 | -1.23 |  | Left Off
PW2 |  | 30.2 | 15.8 | 3 | 51 | 5 | 9 | 1003 | -1.58 |  | Left Off
PW3 |  | 25.4 | 19.9 | 5.5 | 49.2 | 1 | 8 | 1003 | -1.47 |  | Left Off
PW4 |  | 45.6 | 32.1 | 0.5 | 21.8 | 2 | 6 | 1003 | -7.89 |  | Cracked Open
PW5 |  | 28.9 | 25.6 | 0.8 | 44.7 | 0 | 3 | 1003 | -1.23 |  | Left Off
PW6 |  | 24.1 | 21.8 | 1.9 | 52.2 | 9 | 5 | 1003 | -1.14 |  | Left Off
Flare | 14:00 | 49.2 | 35.1 | 0.5 | 15.2 | 7 | 4 | 1003 | 178 |  | Engine running 550 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## March
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-03-04
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To:
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | -0.54 | 1 | 8.8
BK BH 3 | 10:41 | 0.5 | 0.7 | 20.1 | 78.7 | 0 | 0 | 999 | -0.36 | 1 | 3.1
BK BH 4 | 10:43 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 999 | -0.78 | 1 | 5.1
BK BH 5 | 10:46 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 999 | -0.21 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | 0.95 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | -0.63 | 1 | 10
BK BH 8 | 10:55 | 28.5 | 0.8 | 20.2 | 50.5 | 0 | 0 | 999 | 0.25 | 32.2 | 3.6
BK BH 9 | 11:01 | 26.9 | 1.2 | 19.9 | 52 | 0 | 0 | 999 | -0.14 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 999 | 0.25 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 999 | -0.65 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 999 | 0.32 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 999 | -0.17 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 1.5 | 19.1 | 79.4 | 0 | 0 | 999 | 0.36 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 1 | 20.2 | 78.8 | 0 | 0 | 999 | -0.98 | 1 | 17.6
BK BH 16 | 11:35 | 0 | 1.5 | 19.4 | 79.1 | 0 | 0 | 999 | 0.25 | 1 | 11.4
BK BH 17 | 11:42 | 0.4 | 2 | 19.3 | 78.3 | 0 | 0 | 999 | -0.11 | 1 | 12.9
BK BH 18 | 10:08 | 0.4 | 1.1 | 20.1 | 78.4 | 0 | 0 | 999 | 0.75 | 6.8 | 21.2
BK BH 19 | 10:12 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 999 | 0.36 | 1 | 11.2
BK BH 20 | 10:15 | 0.6 | 2.6 | 19.9 | 76.9 | 0 | 0 | 999 | -0.82 | 1 | 10.7
BK BH 21 | 10:20 | 0.7 | 1.1 | 20.2 | 78 | 0 | 0 | 999 | 0.39 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 999 | -0.14 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 999 | 0.27 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 999 | -0.54 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-03-11
Weather: | dry
Wind conditions: | calm
Air Temperature: | 15 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To:
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:15 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 1001 | -0.63 | 1 | 8.8
BK BH 3 | 11:20 | 0.4 | 0.8 | 19.9 | 78.9 | 0 | 0 | 1001 | -0.25 | 1 | 3.1
BK BH 4 | 11:23 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1001 | -0.45 | 1 | 5.1
BK BH 5 | 11:25 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 1001 | -0.28 | 1 | 1.5
BK BH 6 | 11:27 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1001 | -0.65 | 1 | 1.5
BK BH 7 | 11:31 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1001 | 0.35 | 1 | 10
BK BH 8 | 11:34 | 28.1 | 0.8 | 19.9 | 51.2 | 0 | 0 | 1001 | -0.14 | 32.2 | 3.6
BK BH 9 | 11:40 | 27.2 | 1.4 | 20.1 | 51.3 | 0 | 0 | 1001 | 0.25 | 29.6 | 10.4
BK BH 10 | 11:45 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1001 | 0.38 | 1 | 3.9
BK BH 11 | 11:57 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1001 | -0.96 | 1 | 6.5
BK BH 12 | 12:01 | 0 | 1.3 | 19.4 | 79.3 | 0 | 0 | 1001 | 0.15 | 1 | 6.6
BK BH 13 | 12:05 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 1001 | 0.24 | 1 | 9.4
BK BH 14 | 12:08 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 1001 | -0.75 | 1 | 3.5
BK BH 15 | 12:11 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1001 | 0.38 | 1 | 17.6
BK BH 16 | 12:14 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1001 | -0.77 | 1 | 11.4
BK BH 17 | 12:21 | 0.2 | 1.8 | 20.1 | 77.9 | 0 | 0 | 1001 | -0.65 | 1 | 12.9
BK BH 18 | 10:47 | 0.3 | 1.5 | 19.9 | 78.3 | 0 | 0 | 1001 | -78 | 6.8 | 21.2
BK BH 19 | 10:51 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 1001 | 0.63 | 1 | 11.2
BK BH 20 | 10:54 | 0.8 | 2.3 | 19.5 | 77.4 | 0 | 0 | 1001 | -0.87 | 1 | 10.7
BK BH 21 | 10:59 | 0.5 | 1 | 19.8 | 78.7 | 0 | 0 | 1001 | -0.58 | 1 | 21.7
BK BH 23 | 11:04 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 1001 | -0.48 | 1 | 7.3
BK BH 24 | 11:07 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 1001 | -0.25 | 1 | 1.5
BK BH 25 | 11:11 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1001 | 0.86 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-03-18
Weather: | dry
Wind conditions: | calm
Air Temperature: | 6 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To:
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:58 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1004 | 0.42 | 1 | 8.8
BK BH 3 | 11:03 | 0.5 | 1 | 20.1 | 78.4 | 0 | 0 | 1004 | 0.75 | 1 | 3.1
BK BH 4 | 11:05 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 1004 | 0.12 | 1 | 5.1
BK BH 5 | 11:07 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 1004 | 0.29 | 1 | 1.5
BK BH 6 | 11:10 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1004 | -0.23 | 1 | 1.5
BK BH 7 | 11:14 | 0 | 1.4 | 20.2 | 78.4 | 0 | 0 | 1004 | 0.14 | 1 | 10
BK BH 8 | 11:17 | 29 | 1.1 | 19.6 | 50.3 | 0 | 0 | 1004 | -0.53 | 32.2 | 3.6
BK BH 9 | 11:23 | 27.4 | 1.2 | 20 | 51.4 | 0 | 0 | 1004 | 0.26 | 29.6 | 10.4
BK BH 10 | 11:28 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 1004 | -0.75 | 1 | 3.9
BK BH 11 | 11:40 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1004 | 0.14 | 1 | 6.5
BK BH 12 | 11:44 | 0 | 1.7 | 19.9 | 78.4 | 0 | 0 | 1004 | -0.77 | 1 | 6.6
BK BH 13 | 11:48 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 1004 | 0.56 | 1 | 9.4
BK BH 14 | 11:51 | 0 | 1.6 | 20.1 | 78.3 | 0 | 0 | 1004 | 0.34 | 1 | 3.5
BK BH 15 | 11:54 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1004 | -0.15 | 1 | 17.6
BK BH 16 | 11:57 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1004 | 0.26 | 1 | 11.4
BK BH 17 | 12:04 | 0.3 | 1.9 | 20.3 | 77.5 | 0 | 0 | 1004 | 0.31 | 1 | 12.9
BK BH 18 | 10:30 | 0.1 | 1.4 | 19.6 | 78.9 | 0 | 0 | 1004 | 0.87 | 6.8 | 21.2
BK BH 19 | 10:34 | 0 | 2.3 | 19.4 | 78.3 | 0 | 0 | 1004 | 0.9 | 1 | 11.2
BK BH 20 | 10:37 | 0.5 | 2.8 | 19.6 | 77.1 | 0 | 0 | 1004 | -0.75 | 1 | 10.7
BK BH 21 | 10:42 | 0.3 | 1.3 | 19.3 | 79.1 | 0 | 0 | 1004 | -0.14 | 1 | 21.7
BK BH 23 | 10:47 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1004 | 0.21 | 1 | 7.3
BK BH 24 | 10:50 | 0 | 1.2 | 20.2 | 78.6 | 0 | 0 | 1004 | 0.68 | 1 | 1.5
BK BH 25 | 10:54 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 1004 | -0.71 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-03-24
Weather: | dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To:
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:23 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 997 | 0.49 | 1 | 8.8
BK BH 3 | 10:28 | 0.4 | 0.9 | 20.1 | 78.6 | 0 | 0 | 997 | -0.62 | 1 | 3.1
BK BH 4 | 10:30 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 997 | -0.46 | 1 | 5.1
BK BH 5 | 10:32 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 997 | -0.31 | 1 | 1.5
BK BH 6 | 10:35 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.75 | 1 | 1.5
BK BH 7 | 10:39 | 0 | 1.3 | 20.2 | 78.5 | 0 | 0 | 997 | 0.36 | 1 | 10
BK BH 8 | 10:42 | 28.6 | 1.4 | 19.6 | 50.4 | 0 | 0 | 997 | -0.21 | 32.2 | 3.6
BK BH 9 | 10:48 | 26.4 | 1.1 | 20 | 52.5 | 0 | 0 | 997 | 0.46 | 29.6 | 10.4
BK BH 10 | 10:53 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | 0.69 | 1 | 3.9
BK BH 11 | 11:05 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 997 | -0.15 | 1 | 6.5
BK BH 12 | 11:09 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.24 | 1 | 6.6
BK BH 13 | 11:13 | 0 | 1.6 | 19.2 | 79.2 | 0 | 0 | 997 | -0.63 | 1 | 9.4
BK BH 14 | 11:16 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 997 | 0.21 | 1 | 3.5
BK BH 15 | 11:19 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | 0.02 | 1 | 17.6
BK BH 16 | 11:22 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 997 | 0.58 | 1 | 11.4
BK BH 17 | 11:29 | 0.2 | 2.1 | 20.3 | 77.4 | 0 | 0 | 997 | 0.77 | 1 | 12.9
BK BH 18 | 9:55 | 0.4 | 1.9 | 19.6 | 78.1 | 0 | 0 | 997 | -0.96 | 6.8 | 21.2
BK BH 19 | 9:59 | 0 | 2.1 | 19.4 | 78.5 | 0 | 0 | 997 | 0.38 | 1 | 11.2
BK BH 20 | 10:02 | 0.4 | 2.2 | 19.6 | 77.8 | 0 | 0 | 997 | -0.25 | 1 | 10.7
BK BH 21 | 10:07 | 0.6 | 1.9 | 19.3 | 78.2 | 0 | 0 | 997 | 0.14 | 1 | 21.7
BK BH 23 | 10:12 | 0 | 1 | 19.4 | 79.6 | 0 | 0 | 997 | 0.75 | 1 | 7.3
BK BH 24 | 10:15 | 0 | 1.1 | 20.2 | 78.7 | 0 | 0 | 997 | -0.63 | 1 | 1.5
BK BH 25 | 10:19 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | 0.14 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-03-22
Weather: |  | dry + overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 10 | oC
Instrument: |  | GA 2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2016-03-26
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:00 | 50.2 | 36 | 0.6 | 13.2 | 9 | 8 | 999 | 175 |  | Egine running
GV1 |  | 23.6 | 25.9 | 2.7 | 47.8 | 6 | 9 | 999 | -0.05 |  | OFF
GV3 |  | 51.3 | 33.9 | 0.4 | 14.4 | 6 | 6 | 999 | -25.64 |  | Open Full
GV4 |  | 44.5 | 35.9 | 0.9 | 18.7 | 7 | 5 | 999 | -7.89 |  | Cracked Open
GV6 |  | 46.7 | 32.9 | 0.6 | 19.8 | 10 | 8 | 999 | -7.65 |  | Cracked Open
GV7 |  | 23.6 | 25.6 | 2.5 | 48.3 | 9 | 7 | 999 | -1.23 |  | Off Low Gas high o2
GV8 |  | 42.3 | 24.9 | 1.9 | 30.9 | 5 | 8 | 999 | -1.39 |  | Off Low Gas high o3
GV9 |  | 47.8 | 32.6 | 0.8 | 18.8 | 9 | 9 | 999 | -25.93 |  | Open Full
GV10 |  | 40.2 | 24.9 | 1.4 | 33.5 | 8 | 6 | 999 | -1.29 |  | Off
GV11 |  | 33.6 | 25.6 | 0.9 | 39.9 | 8 | 9 | 999 | -1.78 |  | Off
GV12+R3 Manifold |  | 50.5 | 32.6 | 0.4 | 16.5 | 78 | 8 | 999 | -25.69 |  | Open Full
GV12 |  | 51 | 33.5 | 0.5 | 15 | 5 | 8 | 999 | -25.45 |  | Open Full
R3 |  | 50.2 | 31.9 | 0.3 | 17.6 | 2 | 9 | 999 | -25.79 |  | Open Full
GV13 |  | 51.6 | 36.1 | 0.5 | 11.8 | 3 | 6 | 999 | -25.55 |  | Open Full
GV14 |  | 49.9 | 36.9 | 0.4 | 12.8 | 6 | 5 | 999 | -25.69 |  | Open Full
GV15 |  | 51.6 | 34.5 | 0.6 | 13.3 | 9 | 10 | 999 | -24.99 |  | Open Full
GV16 |  | 41.9 | 31.2 | 3 | 23.9 | 8 | 2 | 999 | -1.45 |  | Left OFF
GV17+LC4 Manifold |  | 36.9 | 33.5 | 3.6 | 26 | 9 | 6 | 999 | -1.45 |  | Off at Manifold Gas drops quick.
GV17 |  | 37.5 | 34.9 | 2.9 | 24.7 | 9 | 8 | 999 | -1 |  | Open Full at Well
LC4 |  | 35.9 | 32.6 | 3.9 | 27.6 | 6 | 9 | 999 | -1.24 |  | Open Full at well
GV18 |  | 50.8 | 33.6 | 0.3 | 15.3 | 11 | 7 | 999 | -25.44 |  | Open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 33.6 | 29.9 | 2.5 | 34 | 28 | 4 | 999 | -1.21 |  | Off gas drops off quick.
GV23 |  | 54.6 | 35.1 | 0.3 | 10 | 1 | 12 | 999 | -25.69 |  | Open Full
GV24 |  | 52.3 | 36.4 | 0.4 | 10.9 | 4 | 11 | 999 | -25.98 |  | Open Full
GV25 |  | 52.1 | 36.9 | 0.2 | 10.8 | 6 | 6 | 999 | -25.41 |  | Open Full
GV26 + 27 Manifold |  | 51 | 34.6 | 0.8 | 13.6 | 3 | 8 | 999 | -26.66 |  | Open Full
GV28+ 29 Manifold |  | 50.5 | 35 | 0.5 | 14 | 5 | 9 | 999 | -25.99 |  | Open Full
GV26 |  | 51.5 | 34.9 | 0.8 | 12.8 | 4 | 9 | 999 | -26.84 |  | Open Full
GV27 |  | 50.8 | 34.2 | 0.7 | 14.3 | 25 | 8 | 999 | -26.45 |  | Open Full
GV28 |  | 50.8 | 36.1 | 0.6 | 12.5 | 3 | 7 | 999 | -26.12 |  | Open Full
GV29 |  | 50.3 | 34.8 | 0.4 | 14.5 | 6 | 4 | 999 | -25.84 |  | Open Full
GVA |  | 27.5 | 29.9 | 8.1 | 34.5 | 8 | 2 | 999 | -1.23 |  | Off Low gas
B+C Manifold |  | 47.5 | 36.5 | 0.5 | 15.5 | 5 | 5 | 999 | -25.63 |  | Open Full
GV B |  | 47.1 | 36 | 0.4 | 16.5 | 4 | 8 | 999 | -25.47 |  | Open Full
GV C |  | 48 | 37.4 | 0.6 | 14 | 7 | 6 | 999 | -25.31 |  | Open Full
GV30 |  | 46 | 35.9 | 1 | 17.1 | 8 | 7 | 999 | -7.96 |  | Cracked Open
GV31 |  | 47.1 | 35.9 | 1.1 | 15.9 | 8 | 9 | 999 | -7.25 |  | Cracked Open
GV32 |  | 46.5 | 33.4 | 1 | 19.1 | 9 | 9 | 999 | -8.36 |  | Cracked Open
GV33 |  | 46.8 | 35.6 | 1 | 16.6 | 6 | 21 | 999 | -7.01 |  | Cracked Open
GV34 |  | 46 | 33.6 | 1.2 | 19.2 | 5 | 6 | 999 | -7.36 |  | Cracked Open
GV 35 (New Well) |  | 47.8 | 34.5 | 0.4 | 17.3 | 8 | 9 | 999 | -25.85 |  | Open Full
GV 36 (New Well) |  | 22.3 | 24.1 | 2.6 | 51 | 5 | 6 | 999 | -1.23 |  | OFF low gas.
GV 37 (New Well) |  | 32.6 | 26.6 | 0.8 | 40 | 2 | 3 | 999 | -1.41 |  | OFF low gas.
GV 38 (New Well) |  | 44.9 | 32.6 | 0.8 | 21.7 | 3 | 5 | 999 | -25.13 | -8.63 | Reg cracked Open
GV 39 (New Well) |  | 47 | 33.6 | 0.9 | 18.5 | 6 | 17 | 999 | -25.44 | -8.45 | Reg Cracked Open
GV 40 (New Well) |  | 45.8 | 35 | 1 | 18.2 | 9 | 0 | 999 | -25.63 | -7.99 | Reg cracked Open
GV 41 (New Well) |  | 44 | 34.9 | 1.2 | 19.9 | 6 | 0 | 999 | -7.86 |  | Cracked Open
GV 42 (New Well) |  | 33.6 | 28.9 | 1.2 | 36.3 | 16 | 3 | 999 | -1.23 |  | Off Low Gas
GV 43 (New Well) |  | 45.8 | 33.9 | 1 | 19.3 | 14 | 0 | 999 | -8.63 |  | Cracked Open
GV 44 (New Well) |  | 37.8 | 28.5 | 0.8 | 32.9 | 7 | 2 | 999 | -1.32 |  | Off Low gas
GV 45 (New Well) |  | 45 | 34.5 | 0.8 | 19.7 | 9 | 5 | 999 | -8.56 |  | Cracked Open
GV 46 (New Well) |  | 48 | 39.8 | 0.4 | 11.8 | 18 | 9 | 999 | -25.14 |  | Open Full
GV 47 (New Well) |  | 44.6 | 34.5 | 1 | 19.9 | 5 | 8 | 999 | -8 |  | Cracked Opem
GV 48 (New Well) |  | 59.9 | 39.9 | 0.2 | 2.8311e-15 | 4 | 7 | 999 | -25.39 |  | Open Full
GV 49 (New Well) |  | 46.9 | 27.8 | 1.1 | 24.2 | 5 | 4 | 999 | -1.21 | -7.89 | Reg cracked Open
LC1B |  | 34.6 | 33 | 2.92 | 29.48 | 6 | 5 | 999 | -1.23 |  | OFF
LC2R? |  | 48 | 35.2 | 0.9 | 15.9 | 23 | 8 | 999 | -25.36 |  | Open Full
GV 2.1 |  | 47.5 | 36.9 | 0.7 | 14.9 | 5 | 9 | 999 | -25.63 |  | Open Full
GV 2.2+ LC2B MAN |  | 46.2 | 35 | 1.1 | 17.7 | 4 | 8 | 999 | -8.69 |  | Cracked Open at Manifold
GV 2.2 |  | 47 | 35.6 | 0.9 | 16.5 | 2 | 9 | 999 | -8.78 |  | Cracked Open
LC2B |  | 45.9 | 33.6 | 1.2 | 19.3 | 5 | 7 | 999 | -8.55 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 41 | 33 | 1.4 | 24.6 | 1 | 4 | 999 | -1.35 |  | Off
LC3.1 |  | 41 | 33 | 1.4 | 24.6 | 2 | 5 | 999 | -1.39 |  | Open At well
LC3 |  | 40 | 32 | 2.5 | 25.5 | 4 | 69 | 999 | -1.28 |  | OFF
LC4B |  | 46.7 | 35.6 | 1.3 | 16.4 | 5 | 7 | 999 | -4.56 |  | Cracked Open
R1 + R1B Manifold |  | 48 | 34.5 | 0.6 | 16.9 | 4 | 7 | 999 | -25.36 |  | Open Full
R1 |  | 46.9 | 36.3 | 0.8 | 16 | 44 | 8 | 999 | -7.99 |  | Cracked Open
R1B |  | 49.1 | 35 | 0.4 | 15.5 | 5 | 9 | 999 | -25.98 |  | Open Full
R2B |  | 49.6 | 33.9 | 0.3 | 16.2 | 5 | 3 | 999 | -25.63 |  | Open Full
R4B |  | 48.7 | 34.5 | 0.4 | 16.4 | 4 | 10 | 999 | -25.14 |  | Open Full
R6B |  | 48.6 | 33.6 | 0.2 | 17.6 | 5 | 8 | 999 | -24.98 |  | Open Full
LC5 |  | 48 | 31.9 | 2.2 | 17.9 | 6 | 9 | 999 | 1.23 |  | Left Off ( Gas drops quick)
LC6 |  | 46.6 | 32.6 | 3.1 | 17.7 | 5 | 6 | 999 | -1.06 |  | Left Off ( Gas drops quick)
LC6B |  | 50.2 | 35.6 | 0.8 | 13.4 | 4 | 23 | 999 | -25.69 |  | Open Full
PW1 |  | 0.8 | 0 | 16 | 83.2 | 5 | 8 | 999 | -1.06 |  | Left Off
PW2 |  | 29.9 | 17.4 | 3.5 | 49.2 | 6 | 6 | 999 | -1.06 |  | Left Off
PW3 |  | 26.6 | 18.9 | 4.6 | 49.9 | 5 | 9 | 999 | -1.34 |  | Left Off
PW4 |  | 46 | 33.5 | 0.4 | 20.1 | 2 | 6 | 999 | -7.56 |  | Cracked Open
PW5 |  | 19 | 24.9 | 0.9 | 55.2 | 3 | 3 | 999 | -1.36 |  | Left Off
PW6 |  | 25 | 22.3 | 1.5 | 51.2 | 2 | 9 | 999 | -1.06 |  | Left Off
Flare | 14:05 | 50.4 | 36.5 | 0.5 | 12.6 | 8 | 5 | 999 | 178 |  | Engine running 550 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## April
Date | 2016-04-07
Weather: | dry
Wind conditions: | calm
Air Temperature: | 14 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 999 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.3 | 1 | 19.9 | 78.8 | 0 | 0 | 999 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:29 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.58 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 999 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | 0.84 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 28.9 | 1.6 | 19.9 | 49.6 | 0 | 0 | 999 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:46 | 27 | 1.4 | 19.8 | 51.8 | 0 | 0 | 999 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 999 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 999 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:12 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 999 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 999 | 0.41 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 999 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.3 | 1.8 | 19.9 | 78 | 0 | 0 | 999 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.2 | 1.6 | 19.7 | 78.5 | 0 | 0 | 999 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 999 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.2 | 2.5 | 19.5 | 77.8 | 0 | 0 | 999 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.4 | 2 | 19.4 | 78.2 | 0 | 0 | 999 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 999 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 1 | 20 | 79 | 0 | 0 | 999 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 999 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-04-14
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:52 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1002 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:57 | 0.2 | 1.2 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.52 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:59 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | 0.45 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 12:01 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1002 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 12:04 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 1002 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 12:08 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1002 | 0.42 | 1 | 10 | 0.5 | 5
BK BH 8 | 12:11 | 29 | 1.9 | 19.8 | 49.3 | 0 | 0 | 1002 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:17 | 27.2 | 1.6 | 20 | 51.2 | 0 | 0 | 1002 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:22 | 0 | 1.8 | 19.6 | 78.6 | 0 | 0 | 1002 | -0.14 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:34 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1002 | 0.75 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:38 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1002 | -0.63 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:42 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | -0.25 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:45 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1002 | 0.24 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:48 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.69 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:51 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | -0.15 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:58 | 0.2 | 1.7 | 19.8 | 78.3 | 0 | 0 | 1002 | -0.42 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:24 | 0.3 | 1.9 | 19.6 | 78.2 | 0 | 0 | 1002 | -0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:28 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 1002 | 0.89 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:31 | 0.3 | 2.1 | 20 | 77.6 | 0 | 0 | 1002 | -0.72 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:36 | 0.3 | 2.3 | 19.5 | 77.9 | 0 | 0 | 1002 | 0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:41 | 0 | 1.2 | 19.4 | 79.4 | 0 | 0 | 1002 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:44 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1002 | 0.74 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:48 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1002 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-04-21
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 997 | -0.36 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.3 | 1.5 | 20 | 78.2 | 0 | 0 | 997 | 0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:52 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 997 | -0.12 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 997 | 0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 997 | -0.52 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 29.3 | 1.8 | 20.1 | 48.8 | 0 | 0 | 997 | 0.65 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 27.5 | 1.5 | 19.8 | 51.2 | 0 | 0 | 997 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | -0.23 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 2 | 20 | 78 | 0 | 0 | 997 | 0.64 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 1.4 | 19.92 | 78.68 | 0 | 0 | 997 | 0.57 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 997 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 997 | 0.54 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 997 | 0.84 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 997 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.3 | 1.5 | 20 | 78.2 | 0 | 0 | 997 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.4 | 1.5 | 19.9 | 78.2 | 0 | 0 | 997 | 0.58 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 997 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.2 | 2.2 | 19.8 | 77.8 | 0 | 0 | 997 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.4 | 2.1 | 19.7 | 77.8 | 0 | 0 | 997 | 0.79 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 1.3 | 19.6 | 79.1 | 0 | 0 | 997 | 0.28 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 1 | 20 | 79 | 0 | 0 | 997 | -0.2 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | -0.11 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-04-28
Weather: | dry
Wind conditions: | calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:06 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 999 | -0.56 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:11 | 0.2 | 1.5 | 20.1 | 78.2 | 0 | 0 | 999 | 0.42 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:12 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 999 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:14 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | -0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:18 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 999 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:22 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 999 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:25 | 29.1 | 1.8 | 20 | 49.1 | 0 | 0 | 999 | -0.47 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:31 | 26.9 | 1.5 | 19.9 | 51.7 | 0 | 0 | 999 | 0.96 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:36 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 999 | 0.52 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:48 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 999 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:52 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 999 | 0.36 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:56 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 999 | -0.42 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:59 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 999 | 0.18 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:02 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 999 | -0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:05 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | 0.14 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:12 | 0.2 | 1.5 | 20 | 78.3 | 0 | 0 | 999 | 0.75 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:38 | 0.5 | 1.5 | 19.6 | 78.4 | 0 | 0 | 999 | -0.86 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:42 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 999 | 0.35 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:45 | 0.3 | 2.2 | 19.9 | 77.6 | 0 | 0 | 999 | -0.77 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:50 | 0.2 | 2.1 | 19.4 | 78.3 | 0 | 0 | 999 | -0.86 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:55 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 999 | -0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:58 | 0 | 1 | 20.1 | 78.9 | 0 | 0 | 999 | 0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:02 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | 0.47 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-04-19
Weather: |  | dry + overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 18 | oC
Instrument: |  | GEM 2000 Plus | (with H2s filter fitted)
Serial No: |  | GM12289/10
Calibrated To: |  | 2016-09-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 9:30 | 51.6 | 37.9 | 0.5 | 10 | 10 | 7 | 1004 | 170 |  | Egine running
GV1 |  | 22.6 | 24.5 | 2.5 | 50.4 | 5 | 7 | 1004 | -0.45 |  | OFF
GV3 |  | 50.2 | 35.8 | 0.5 | 13.5 | 6 | 9 | 1004 | -27.65 |  | Open Full
GV4 |  | 45.9 | 36.9 | 1 | 16.2 | 5 | 4 | 1004 | -8.62 |  | Cracked Open
GV6 |  | 44.8 | 33.6 | 0.9 | 20.7 | 6 | 7 | 1004 | -8.63 |  | Cracked Open
GV7 |  | 25.6 | 21.9 | 2.4 | 50.1 | 5 | 8 | 1004 | -1.06 |  | Off Low Gas high o2
GV8 |  | 39.9 | 25.5 | 1.1 | 33.5 | 4 | 7 | 1004 | -1.45 |  | Off Low Gas high o3
GV9 |  | 48 | 33.5 | 0.6 | 17.9 | 4 | 4 | 1004 | -27.12 |  | Open Full
GV10 |  | 44.5 | 30.1 | 1.3 | 24.1 | 1 | 11 | 1004 | -1.56 |  | Off
GV11 |  | 38.6 | 26.5 | 1.1 | 33.8 | 4 | 9 | 1004 | -1.13 |  | Off
GV12+R3 Manifold |  | 51 | 33.5 | 0.5 | 15 | 5 | 6 | 1004 | -26.99 |  | Open Full
GV12 |  | 51.2 | 33.2 | 0.4 | 15.2 | 6 | 9 | 1004 | -26.87 |  | Open Full
R3 |  | 50.5 | 33.7 | 0.6 | 15.2 | 5 | 8 | 1004 | -27.03 |  | Open Full
GV13 |  | 50 | 35.9 | 0.4 | 13.7 | 4 | 9 | 1004 | -27.98 |  | Open Full
GV14 |  | 49.8 | 37.8 | 0.6 | 11.8 | 2 | 8 | 1004 | -27.54 |  | Open Full
GV15 |  | 50.6 | 33.8 | 0.8 | 14.8 | 5 | 14 | 1004 | -26.59 |  | Open Full
GV16 |  | 41.5 | 33.2 | 2.8 | 22.5 | 3 | 11 | 1004 | -1.22 |  | Left OFF
GV17+LC4 Manifold |  | 37.9 | 32.8 | 3.2 | 26.1 | 9 | 8 | 1004 | -1.23 |  | Off at Manifold Gas drops quick.
GV17 |  | 38.2 | 33.1 | 2.6 | 26.1 | 13 | 7 | 1004 | -1 |  | Open Full at Well
LC4 |  | 36.8 | 32.6 | 3.5 | 27.1 | 2 | 8 | 1004 | -1.36 |  | Open Full at well
GV18 |  | 52.3 | 37 | 0.4 | 10.3 | 5 | 9 | 1004 | -27.89 |  | Open Full
Point: GV19; %: 100; ppm: 3 |  |  | N/A Going to decommission.
GV 22 |  | 35.9 | 30.5 | 2.2 | 31.4 | 6 | 9 | 1004 | -1.06 |  | Off gas drops off quick.
GV23 |  | 53.6 | 35.8 | 0.4 | 10.2 | 5 | 8 | 1004 | -26.35 |  | Open Full
GV24 |  | 53.1 | 37 | 0.5 | 9.4 | 4 | 8 | 1004 | -27.87 |  | Open Full
GV25 |  | 52.6 | 36.5 | 0.4 | 10.5 | 5 | 9 | 1004 | -27.14 |  | Open Full
GV26 + 27 Manifold |  | 51.5 | 35.6 | 0.5 | 12.4 | 5 | 6 | 1004 | -27.3 |  | Open Full
GV28+ 29 Manifold |  | 51 | 35.6 | 0.3 | 13.1 | 4 | 4 | 1004 | -26.89 |  | Open Full
GV26 |  | 51.9 | 34.9 | 0.4 | 12.8 | 2 | 10 | 1004 | -27.87 |  | Open Full
GV27 |  | 51 | 35.9 | 0.6 | 12.5 | 5 | 21 | 1004 | -27 |  | Open Full
GV28 |  | 51.2 | 35.8 | 0.2 | 12.8 | 4 | 9 | 1004 | -26.36 |  | Open Full
GV29 |  | 50.4 | 35 | 0.5 | 14.1 | 7 | 5 | 1004 | -27.01 |  | Open Full
GVA |  | 28.5 | 20.5 | 7.5 | 43.5 | 8 | 1 | 1004 | -1.14 |  | Off Low gas
B+C Manifold |  | 46.9 | 37 | 0.4 | 15.7 | 9 | 4 | 1004 | -26.03 |  | Open Full
GV B |  | 47 | 36.9 | 0.5 | 15.6 | 6 | 7 | 1004 | -27.45 |  | Open Full
GV C |  | 46.5 | 37 | 0.3 | 16.2 | 14 | 8 | 1004 | -26.89 |  | Open Full
GV30 |  | 47 | 36 | 0.9 | 16.1 | 7 | 7 | 1004 | -8.06 |  | Cracked Open
GV31 |  | 46.9 | 35.9 | 1.1 | 16.1 | 4 | 7 | 1004 | -7.11 |  | Cracked Open
GV32 |  | 45.5 | 33.4 | 1.1 | 20 | 2 | 7 | 1004 | -8.06 |  | Cracked Open
GV33 |  | 45.2 | 35.2 | 0.8 | 18.8 | 5 | 8 | 1004 | -7.89 |  | Cracked Open
GV34 |  | 45.9 | 34 | 1.1 | 19 | 4 | 6 | 1004 | -7.36 |  | Cracked Open
GV 35 (New Well) |  | 48.9 | 33.6 | 0.5 | 17 | 7 | 5 | 1004 | -27.45 |  | Open Full
GV 36 (New Well) |  | 25.9 | 25.4 | 2.8 | 45.9 | 8 | 6 | 1004 | -1.25 |  | OFF low gas.
GV 37 (New Well) |  | 33.4 | 27.8 | 1.1 | 37.7 | 5 | 7 | 1004 | -1.54 |  | OFF low gas.
GV 38 (New Well) |  | 45.2 | 33.8 | 0.9 | 20.1 | 4 | 9 | 1004 | -27.48 |  | Cracked Open
GV 39 (New Well) |  | 46.9 | 34.9 | 1.1 | 17.1 | 8 | 1 | 1004 | -26.89 |  | Cracked Open
GV 40 (New Well) |  | 44.9 | 35.6 | 1 | 18.5 | 5 | 7 | 1004 | -26.58 |  | Cracked Open
GV 41 (New Well) |  | 44.5 | 35 | 1 | 19.5 | 6 | 28 | 1004 | -8 |  | Cracked Open
GV 42 (New Well) |  | 37.9 | 30 | 1.4 | 30.7 | 12 | 6 | 1004 | -1.07 |  | Off Low Gas
GV 43 (New Well) |  | 42.6 | 35.8 | 1.5 | 20.1 | 8 | 9 | 1004 | -7.93 | -1.21 | Reg closed o2 rose
GV 44 (New Well) |  | 38 | 29.9 | 0.7 | 31.4 | 5 | 8 | 1004 | -1.24 |  | Off Low gas
GV 45 (New Well) |  | 45.8 | 36.9 | 1 | 16.3 | 4 | 4 | 1004 | -7.99 |  | Cracked Open
GV 46 (New Well) |  | 48.5 | 40 | 0.5 | 11 | 7 | 7 | 1004 | -26.97 |  | Open Full
GV 47 (New Well) |  | 46 | 35.1 | 1 | 17.9 | 7 | 8 | 1004 | -6.99 |  | Cracked Opem
GV 48 (New Well) |  | 59.6 | 40 | 0.1 | 0.3 | 7 | 8 | 1004 | -26.59 |  | Open Full
GV 49 (New Well) |  | 45.1 | 32.5 | 1.1 | 21.3 | 4 | 5 | 1004 | -1.35 |  | Cracked open
LC1B |  | 36.9 | 34.5 | 2.6 | 26 | 1 | 3 | 1004 | -1.06 |  | OFF
LC2R? |  | 47.5 | 36.9 | 0.8 | 14.8 | 4 | 3 | 1004 | -26.99 |  | Open Full
GV 2.1 |  | 48 | 37.9 | 0.6 | 13.5 | 7 | 9 | 1004 | -27.87 |  | Open Full
GV 2.2+ LC2B MAN |  | 46.5 | 35.2 | 1 | 17.3 | 5 | 6 | 1004 | -7.99 |  | Cracked Open at Manifold
GV 2.2 |  | 47.1 | 36 | 0.9 | 16 | 8 | 7 | 1004 | -8.06 |  | Cracked Open
LC2B |  | 46.4 | 34.5 | 1.1 | 18 | 5 | 11 | 1004 | -7.89 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 42.3 | 34.5 | 1.3 | 21.9 | 2 | 8 | 1004 | -1.41 |  | Off
LC3.1 |  | 42.3 | 34.5 | 1.3 | 21.9 | 4 | 9 | 1004 | -1.45 |  | Open At well
LC3 |  | 41.6 | 35.9 | 2.4 | 20.1 | 9 | 45 | 1004 | -1.39 |  | OFF
LC4B |  | 46.9 | 36.9 | 1.2 | 15 | 14 | 5 | 1004 | -5.89 |  | Cracked Open
R1 + R1B Manifold |  | 48.2 | 35 | 0.7 | 16.1 | 4 | 12 | 1004 | -26.98 |  | Open Full
R1 |  | 47.2 | 35.8 | 0.6 | 16.4 | 6 | 8 | 1004 | -8.45 |  | Cracked Open
R1B |  | 49.3 | 34.2 | 0.8 | 15.7 | 8 | 7 | 1004 | -26.97 |  | Open Full
R2B |  | 50.1 | 36.8 | 0.4 | 12.7 | 11 | 2 | 1004 | -27.01 |  | Open Full
R4B |  | 48.9 | 35.6 | 0.2 | 15.3 | 4 | 1 | 1004 | -27 |  | Open Full
R6B |  | 49.9 | 32.6 | 0.3 | 17.2 | 5 | 9 | 1004 | -26.89 |  | Open Full
LC5 |  | 47.5 | 32.5 | 2.4 | 17.6 | 9 | 6 | 1004 | 0.21 |  | Left Off ( Gas drops quick)
LC6 |  | 46 | 33.9 | 3.5 | 16.6 | 6 | 9 | 1004 | 0.89 |  | Left Off ( Gas drops quick)
LC6B |  | 50.4 | 36.8 | 0.7 | 12.1 | 9 | 8 | 1004 | -27.48 |  | Open Full
PW1 |  | 0.6 | 0 | 15.2 | 84.2 | 11 | 5 | 1004 | -1 |  | Left Off
PW2 |  | 32.6 | 15.6 | 3.2 | 48.6 | 6 | 7 | 1004 | -0.89 |  | Left Off
PW3 |  | 29.9 | 19.9 | 5 | 45.2 | 6 | 8 | 1004 | -1.21 |  | Left Off
PW4 |  | 45.2 | 34.9 | 0.3 | 19.6 | 8 | 5 | 1004 | -6.58 |  | Cracked Open
PW5 |  | 21.9 | 22.5 | 1 | 54.6 | 9 | 8 | 1004 | -1 |  | Left Off
PW6 |  | 26 | 20.9 | 1.9 | 51.2 | 7 | 9 | 1004 | -1.03 |  | Left Off
Flare | 13:45 | 51.5 | 37.2 | 0.4 | 10.9 | 10 | 7 | 1004 | 170 |  | Engine running 550 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## May
Date | 05/052016
Weather: | dry
Wind conditions: | calm
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:29 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1002 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:34 | 0.3 | 1.3 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.71 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:36 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.54 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:39 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 1002 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:41 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1002 | 0.68 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:45 | 0 | 1.3 | 19.7 | 79 | 0 | 0 | 1002 | -0.29 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:48 | 29 | 1.5 | 19.8 | 49.7 | 0 | 0 | 1002 | 0.68 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:54 | 27.1 | 1.7 | 20.1 | 51.1 | 0 | 0 | 1002 | 0.42 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:59 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1002 | 0.59 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:11 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 1002 | 0.24 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:15 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.89 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:19 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1002 | 0.52 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:22 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1002 | 0.47 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:25 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | -0.18 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:28 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1002 | 0.62 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:35 | 0.3 | 1.7 | 19.5 | 78.5 | 0 | 0 | 1002 | 0.47 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:01 | 0.4 | 1.6 | 19.8 | 78.2 | 0 | 0 | 1002 | -0.51 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:05 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1002 | 0.12 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:08 | 0.2 | 2.4 | 20 | 77.4 | 0 | 0 | 1002 | 0.67 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:13 | 0.3 | 2.3 | 19.6 | 77.8 | 0 | 0 | 1002 | -0.35 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:18 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1002 | 0.84 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:21 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1002 | 0.38 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:25 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 12/052016
Weather: | dry
Wind conditions: | calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:40 | 0 | 1.7 | 19.9 | 78.4 | 0 | 0 | 997 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:45 | 0.4 | 1.4 | 19.5 | 78.7 | 0 | 0 | 997 | 0.26 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:47 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | -0.11 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:50 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 997 | 0.35 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:52 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 997 | 0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:56 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | -0.26 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:59 | 28.6 | 1.4 | 20 | 50 | 0 | 0 | 997 | -0.36 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:05 | 27.5 | 1.5 | 20 | 51 | 0 | 0 | 997 | -0.5 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:10 | 0 | 1.8 | 19.6 | 78.6 | 0 | 0 | 997 | -0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:22 | 0 | 2.2 | 19.5 | 78.3 | 0 | 0 | 997 | -0.23 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:26 | 0 | 1.2 | 20.4 | 78.4 | 0 | 0 | 997 | 0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:30 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 997 | 0.52 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:33 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 997 | 0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:36 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 997 | 0.65 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:39 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 997 | -0.75 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:46 | 0.2 | 1.5 | 19.9 | 78.4 | 0 | 0 | 997 | 0.58 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:12 | 0.5 | 1.9 | 19.9 | 77.7 | 0 | 0 | 997 | 0.57 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:16 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 997 | -0.23 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:19 | 0.3 | 2.1 | 19.5 | 78.1 | 0 | 0 | 997 | 0.14 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:24 | 0.5 | 2 | 20 | 77.5 | 0 | 0 | 997 | -0.72 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:29 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 997 | 0.34 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:32 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 997 | 0.68 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:36 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | 0.47 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 19/052016
Weather: | dry
Wind conditions: | calm
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 999 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.3 | 1.1 | 20 | 78.6 | 0 | 0 | 999 | 0.32 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:52 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | -0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 999 | 0.28 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 999 | 0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 999 | -0.65 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 29 | 1.8 | 19.6 | 49.6 | 0 | 0 | 999 | 0.34 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 27.7 | 1.4 | 19.8 | 51.1 | 0 | 0 | 999 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 999 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 999 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 999 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 999 | 0.69 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 999 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 999 | 0.23 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 999 | -0.42 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.3 | 1.4 | 19.6 | 78.7 | 0 | 0 | 999 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.4 | 2 | 19.7 | 77.9 | 0 | 0 | 999 | -0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 1.8 | 19.2 | 79 | 0 | 0 | 999 | -0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.2 | 2 | 19.7 | 78.1 | 0 | 0 | 999 | 0.6 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.4 | 1.8 | 19.8 | 78 | 0 | 0 | 999 | 0.27 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 999 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 999 | -0.58 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-05-26
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | -0.35 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.2 | 1 | 19.5 | 79.3 | 0 | 0 | 1002 | 0.76 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1002 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1002 | -0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.52 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | 0.48 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 28.7 | 1.5 | 19.9 | 49.9 | 0 | 0 | 1002 | -0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 27.4 | 1.2 | 20 | 51.4 | 0 | 0 | 1002 | 0.36 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | -0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 2 | 20 | 78 | 0 | 0 | 1002 | 0.16 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1002 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1002 | 0.35 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1002 | -0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 1002 | 0.48 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.4 | 1.5 | 19.8 | 78.3 | 0 | 0 | 1002 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.2 | 2.1 | 19.9 | 77.8 | 0 | 0 | 1002 | 0.25 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 1002 | 0.69 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.3 | 2.4 | 19.8 | 77.5 | 0 | 0 | 1002 | -0.17 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.3 | 1.5 | 19.9 | 78.3 | 0 | 0 | 1002 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.39 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1002 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 1.1 | 20.2 | 78.7 | 0 | 0 | 1002 | 0.28 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-05-24
Weather: |  | dry + overcast
Wind conditions: |  | Breezy
Air Temperature: |  | 19 | oC
Instrument: |  | GEM 2000 Plus | (with H2s filter fitted)
Serial No: |  | GM12289/10
Calibrated To: |  | 2016-09-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 9:30 | 50.4 | 38.4 | 0.4 | 10.8 | 12 | 8 | 997 | 165 |  | Egine running
GV1 |  | 23.8 | 25.9 | 2.1 | 48.2 | 4 | 5 | 997 | -0.46 |  | OFF
GV3 |  | 51.6 | 37.4 | 0.6 | 10.4 | 5 | 9 | 997 | -28.49 |  | Open Full
GV4 |  | 44.9 | 36.5 | 1.1 | 17.5 | 6 | 8 | 997 | -7.89 |  | Cracked Open
GV6 |  | 44.5 | 34.5 | 1 | 20 | 7 | 7 | 997 | -6.85 |  | Cracked Open
GV7 |  | 26.9 | 23.7 | 2.3 | 47.1 | 7 | 9 | 997 | -1.09 |  | Off Low Gas high o2
GV8 |  | 38.5 | 26.5 | 1.4 | 33.6 | 6 | 5 | 997 | -1.24 |  | Off Low Gas high o3
GV9 |  | 48.5 | 35.9 | 0.5 | 15.1 | 6 | 6 | 997 | -28.13 |  | Open Full
GV10 |  | 43.9 | 32.5 | 1.2 | 22.4 | 2 | 12 | 997 | -1.23 |  | Off
GV11 |  | 40 | 27.5 | 1.3 | 31.2 | 6 | 10 | 997 | -1.78 |  | Off
GV12+R3 Manifold |  | 50.8 | 35.6 | 0.5 | 13.1 | 8 | 7 | 997 | -28.09 |  | Open Full
GV12 |  | 50.6 | 36 | 0.3 | 13.1 | 7 | 11 | 997 | -27.89 |  | Open Full
R3 |  | 51 | 34.5 | 0.6 | 13.9 | 6 | 6 | 997 | -28.34 |  | Open Full
GV13 |  | 51.5 | 37 | 0.8 | 10.7 | 5 | 10 | 997 | -28.33 |  | Open Full
GV14 |  | 48.6 | 36.9 | 0.4 | 14.1 | 4 | 9 | 997 | -28.81 |  | Open Full
GV15 |  | 50 | 34.5 | 0.5 | 15 | 6 | 12 | 997 | -28.47 |  | Open Full
GV16 |  | 42.5 | 34.2 | 3 | 20.3 | 4 | 9 | 997 | -1.32 |  | Left OFF
GV17+LC4 Manifold |  | 38.5 | 33.6 | 3 | 24.9 | 10 | 10 | 997 | -1.06 |  | Off at Manifold Gas drops quick.
GV17 |  | 39 | 34 | 2.4 | 24.6 | 11 | 8 | 997 | -1.23 |  | Open Full at Well
LC4 |  | 37.5 | 31.8 | 3.3 | 27.4 | 4 | 10 | 997 | -0.89 |  | Open Full at well
GV18 |  | 52.8 | 36.9 | 0.5 | 9.8 | 6 | 7 | 997 | -28.85 |  | Open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 36.2 | 31.5 | 2.5 | 29.8 | 7 | 10 | 997 | -1.09 |  | Off gas drops off quick.
GV23 |  | 52.9 | 36.2 | 0.5 | 10.4 | 4 | 7 | 997 | -28.59 |  | Open Full
GV24 |  | 53.6 | 37.8 | 0.6 | 8 | 6 | 6 | 997 | -28.79 |  | Open Full
GV25 |  | 53.1 | 35.6 | 0.4 | 10.9 | 9 | 10 | 997 | -28 |  | Open Full
GV26 + 27 Manifold |  | 52 | 36 | 0.6 | 11.4 | 4 | 12 | 997 | -28.56 |  | Open Full
GV28+ 29 Manifold |  | 51.2 | 35.9 | 0.4 | 12.5 | 5 | 5 | 997 | -28.41 |  | Open Full
GV26 |  | 52.4 | 35.2 | 0.5 | 11.9 | 4 | 10 | 997 | -28.59 |  | Open Full
GV27 |  | 51.4 | 36.5 | 0.7 | 11.4 | 6 | 18 | 997 | -28.45 |  | Open Full
GV28 |  | 51.4 | 36.5 | 0.2 | 11.9 | 5 | 10 | 997 | -28.09 |  | Open Full
GV29 |  | 50.7 | 35.2 | 0.6 | 13.5 | 6 | 5 | 997 | -28.49 |  | Open Full
GVA |  | 30.1 | 22.3 | 8 | 39.6 | 9 | 4 | 997 | -1.26 |  | Off Low gas
B+C Manifold |  | 48.5 | 36.9 | 0.5 | 14.1 | 10 | 9 | 997 | -28.49 |  | Open Full
GV B |  | 47.5 | 36.5 | 0.5 | 15.5 | 7 | 8 | 997 | -28.06 |  | Open Full
GV C |  | 48.9 | 37.2 | 0.4 | 13.5 | 11 | 8 | 997 | -28.58 |  | Open Full
GV30 |  | 48.5 | 37.5 | 0.5 | 13.5 | 9 | 9 | 997 | -7.59 | -28.57 | Reg Opened Full
GV31 |  | 45.5 | 36 | 1 | 17.5 | 8 | 10 | 997 | -7.29 |  | Cracked Open
GV32 |  | 44.9 | 35.4 | 1.2 | 18.5 | 4 | 5 | 997 | -7.89 |  | Cracked Open
GV33 |  | 45 | 35.4 | 1 | 18.6 | 7 | 9 | 997 | -7.24 |  | Cracked Open
GV34 |  | 45.8 | 33.9 | 1 | 19.3 | 5 | 7 | 997 | -7.55 |  | Cracked Open
GV 35 (New Well) |  | 49.2 | 34.5 | 0.4 | 15.9 | 10 | 9 | 997 | -28.76 |  | Open Full
GV 36 (New Well) |  | 38.9 | 25.4 | 2.5 | 33.2 | 3 | 10 | 997 | -1.45 |  | OFF low gas.
GV 37 (New Well) |  | 34.5 | 26.9 | 1.4 | 37.2 | 9 | 6 | 997 | -1.23 |  | OFF low gas.
GV 38 (New Well) |  | 46.2 | 34.5 | 0.8 | 18.5 | 8 | 10 | 997 | -28.59 |  | Cracked Open
GV 39 (New Well) |  | 46 | 36.1 | 1 | 16.9 | 9 | 5 | 997 | -28.47 |  | Cracked Open
GV 40 (New Well) |  | 45.2 | 36 | 1.1 | 17.7 | 5 | 9 | 997 | -28.11 |  | Cracked Open
GV 41 (New Well) |  | 44.1 | 34.5 | 1 | 20.4 | 7 | 22 | 997 | -7.59 |  | Cracked Open
GV 42 (New Well) |  | 38.1 | 32.2 | 1.5 | 28.2 | 12 | 9 | 997 | -1.26 |  | Off Low Gas
GV 43 (New Well) |  | 46.2 | 36.6 | 1.1 | 16.1 | 15 | 10 | 997 | -1.32 | -8.06 | Reg cracked Open
GV 44 (New Well) |  | 37.8 | 30.1 | 0.8 | 31.3 | 13 | 7 | 997 | -1.33 |  | Off Low gas
GV 45 (New Well) |  | 44.9 | 37 | 1.1 | 17 | 11 | 5 | 997 | -7.59 |  | Cracked Open
GV 46 (New Well) |  | 47.9 | 39.9 | 0.4 | 11.8 | 9 | 8 | 997 | -28.01 |  | Open Full
GV 47 (New Well) |  | 46.2 | 36.6 | 1.1 | 16.1 | 8 | 10 | 997 | -7.06 |  | Cracked Opem
GV 48 (New Well) |  | 59.9 | 39.9 | 0.1 | 0.1 | 9 | 9 | 997 | -28.09 |  | Open Full
GV 49 (New Well) |  | 45.3 | 33.6 | 1 | 20.1 | 10 | 8 | 997 | -7.04 |  | Cracked open
LC1B |  | 37.5 | 35.6 | 2.2 | 24.7 | 4 | 9 | 997 | -1.25 |  | OFF
LC2R? |  | 48.1 | 37.2 | 0.7 | 14 | 7 | 7 | 997 | -28.59 |  | Open Full
GV 2.1 |  | 48.3 | 38 | 0.5 | 13.2 | 9 | 10 | 997 | -28.07 |  | Open Full
GV 2.2+ LC2B MAN |  | 47 | 36.1 | 1.1 | 15.8 | 9 | 8 | 997 | -7.25 |  | Cracked Open at Manifold
GV 2.2 |  | 47.5 | 36.8 | 1 | 14.7 | 4 | 9 | 997 | -7.11 |  | Cracked Open
LC2B |  | 46.8 | 35.5 | 1.2 | 16.5 | 5 | 12 | 997 | -7.99 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 43.6 | 35.6 | 1.2 | 19.6 | 7 | 7 | 997 | -1.25 |  | Off
LC3.1 |  | 44 | 35 | 1 | 20 | 9 | 10 | 997 | -1.11 |  | Open At well
LC3 |  | 42.6 | 34.9 | 1.8 | 20.7 | 7 | 26 | 997 | -1.41 |  | OFF
LC4B |  | 46.1 | 37 | 1.1 | 15.8 | 8 | 7 | 997 | -6.09 |  | Cracked Open
R1 + R1B Manifold |  | 48.2 | 35.6 | 0.8 | 15.4 | 6 | 11 | 997 | -28.57 |  | Open Full
R1 |  | 45.8 | 35 | 1.1 | 18.1 | 6 | 9 | 997 | -9.25 |  | Cracked Open
R1B |  | 50.2 | 38 | 0.4 | 11.4 | 9 | 8 | 997 | -28.88 |  | Open Full
R2B |  | 51.2 | 36.1 | 0.3 | 12.4 | 8 | 5 | 997 | -28.57 |  | Open Full
R4B |  | 49.2 | 35.1 | 0.5 | 15.2 | 8 | 3 | 997 | -28.36 |  | Open Full
R6B |  | 50.5 | 33.6 | 0.4 | 15.5 | 9 | 8 | 997 | -28.77 |  | Open Full
LC5 |  | 48.1 | 33.6 | 2.1 | 16.2 | 5 | 7 | 997 | 0.56 |  | Left Off ( Gas drops quick)
LC6 |  | 47.2 | 34.5 | 3 | 15.3 | 7 | 10 | 997 | -0.25 |  | Left Off ( Gas drops quick)
LC6B |  | 51.4 | 36.5 | 0.5 | 11.6 | 10 | 7 | 997 | -28.57 |  | Open Full
PW1 |  | 0.9 | 0 | 16 | 83.1 | 12 | 8 | 997 | -1.25 |  | Left Off
PW2 |  | 33.5 | 16.8 | 3.5 | 46.2 | 9 | 9 | 997 | -0.89 |  | Left Off
PW3 |  | 32.4 | 20.4 | 4.9 | 42.3 | 5 | 10 | 997 | -1.25 |  | Left Off
PW4 |  | 45.8 | 35.9 | 1.1 | 17.2 | 7 | 7 | 997 | -7.58 |  | Cracked Open
PW5 |  | 22.4 | 23.9 | 1.6 | 52.1 | 11 | 9 | 997 | -1.23 |  | Left Off
PW6 |  | 29.8 | 22.7 | 2.6 | 44.9 | 8 | 11 | 997 | -1.09 |  | Left Off
Flare | 13:45 | 50.9 | 38.9 | 0.3 | 9.9 | 11 | 9 | 997 | 165 |  | Engine running 550 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## June
Date | 2016-06-02
Weather: | dry
Wind conditions: | calm
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:48 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1006 | -0.52 | 1 | 8.8
BK BH 3 | 10:53 | 0.3 | 0.8 | 19.7 | 79.2 | 0 | 0 | 1006 | 0.23 | 1 | 3.1
BK BH 4 | 10:54 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1006 | 0.45 | 1 | 5.1
BK BH 5 | 10:56 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 1006 | 0.21 | 1 | 1.5
BK BH 6 | 11:00 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 1006 | 0.18 | 1 | 1.5
BK BH 7 | 11:04 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1006 | -0.45 | 1 | 10
BK BH 8 | 11:07 | 28.5 | 1.3 | 19.6 | 50.6 | 0 | 0 | 1006 | 0.68 | 32.2 | 3.6
BK BH 9 | 11:13 | 27 | 1 | 19.8 | 52.2 | 0 | 0 | 1006 | -0.19 | 29.6 | 10.4
BK BH 10 | 11:18 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1006 | 0.38 | 1 | 3.9
BK BH 11 | 11:30 | 0 | 1.8 | 20.1 | 78.1 | 0 | 0 | 1006 | -0.45 | 1 | 6.5
BK BH 12 | 11:34 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1006 | -0.62 | 1 | 6.6
BK BH 13 | 11:38 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1006 | 0.54 | 1 | 9.4
BK BH 14 | 11:41 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 1006 | -0.75 | 1 | 3.5
BK BH 15 | 11:44 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 1006 | 0.62 | 1 | 17.6
BK BH 16 | 11:47 | 0 | 2 | 20 | 78 | 0 | 0 | 1006 | -0.38 | 1 | 11.4
BK BH 17 | 11:54 | 0.3 | 1.4 | 19.6 | 78.7 | 0 | 0 | 1006 | -0.42 | 1 | 12.9
BK BH 18 | 10:20 | 0.1 | 2.5 | 19.8 | 77.6 | 0 | 0 | 1006 | 0.28 | 6.8 | 21.2
BK BH 19 | 10:24 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1006 | -0.58 | 1 | 11.2
BK BH 20 | 10:27 | 0.3 | 2.5 | 19.5 | 77.7 | 0 | 0 | 1006 | -0.36 | 1 | 10.7
BK BH 21 | 10:32 | 0.2 | 1.9 | 19.7 | 78.2 | 0 | 0 | 1006 | -0.89 | 1 | 21.7
BK BH 23 | 10:37 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1006 | 0.27 | 1 | 7.3
BK BH 24 | 10:40 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1006 | -0.24 | 1 | 1.5
BK BH 25 | 10:44 | 0 | 1 | 20 | 79 | 0 | 0 | 1006 | -0.28 | 1 | 9.9
Date | 2016-06-09
Weather: | dry
Wind conditions: | calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:10 | 0 | 1.6 | 20.1 | 78.3 | 0 | 0 | 997 | -0.25 | 1 | 8.8
BK BH 3 | 10:15 | 0.2 | 1 | 19.8 | 79 | 0 | 0 | 997 | 0.41 | 1 | 3.1
BK BH 4 | 10:17 | 0 | 1.3 | 19.4 | 79.3 | 0 | 0 | 997 | 0.23 | 1 | 5.1
BK BH 5 | 10:19 | 0 | 1 | 19.7 | 79.3 | 0 | 0 | 997 | 0.58 | 1 | 1.5
BK BH 6 | 10:22 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 997 | 0.26 | 1 | 1.5
BK BH 7 | 10:26 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 997 | 0.45 | 1 | 10
BK BH 8 | 10:29 | 29 | 1.5 | 19.7 | 49.8 | 0 | 0 | 997 | -0.12 | 32.2 | 3.6
BK BH 9 | 10:35 | 26.8 | 1.2 | 19.5 | 52.5 | 0 | 0 | 997 | 0.36 | 29.6 | 10.4
BK BH 10 | 10:40 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 997 | -0.15 | 1 | 3.9
BK BH 11 | 10:52 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 997 | 0.73 | 1 | 6.5
BK BH 12 | 10:56 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | -0.42 | 1 | 6.6
BK BH 13 | 11:00 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 997 | 0.36 | 1 | 9.4
BK BH 14 | 11:03 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 997 | -0.11 | 1 | 3.5
BK BH 15 | 11:06 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 997 | 0.74 | 1 | 17.6
BK BH 16 | 11:09 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | 0.23 | 1 | 11.4
BK BH 17 | 11:16 | 0.2 | 1.6 | 20.1 | 78.1 | 0 | 0 | 997 | -0.18 | 1 | 12.9
BK BH 18 | 9:42 | 0.2 | 2.1 | 20 | 77.7 | 0 | 0 | 997 | 0.92 | 6.8 | 21.2
BK BH 19 | 9:46 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 997 | 0.37 | 1 | 11.2
BK BH 20 | 9:49 | 0.1 | 2.3 | 19.9 | 77.7 | 0 | 0 | 997 | -0.18 | 1 | 10.7
BK BH 21 | 9:54 | 0.4 | 2 | 20 | 77.6 | 0 | 0 | 997 | 0.29 | 1 | 21.7
BK BH 23 | 9:59 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 997 | -0.11 | 1 | 7.3
BK BH 24 | 10:02 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 997 | 0.54 | 1 | 1.5
BK BH 25 | 10:06 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | 0.87 | 1 | 9.9
Date | 2016-06-16
Weather: | dry
Wind conditions: | calm
Air Temperature: | 20 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:36 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.49 | 1 | 8.8
BK BH 3 | 10:41 | 0.3 | 1.2 | 20 | 78.5 | 0 | 0 | 999 | -0.62 | 1 | 3.1
BK BH 4 | 10:43 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 999 | 0.32 | 1 | 5.1
BK BH 5 | 10:46 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 999 | 0.87 | 1 | 1.5
BK BH 6 | 10:48 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 999 | 0.75 | 1 | 1.5
BK BH 7 | 10:52 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.36 | 1 | 10
BK BH 8 | 10:55 | 29.4 | 1.3 | 19.9 | 49.4 | 0 | 0 | 999 | -0.21 | 32.2 | 3.6
BK BH 9 | 11:01 | 26.5 | 1 | 19.2 | 53.3 | 0 | 0 | 999 | 0.46 | 29.6 | 10.4
BK BH 10 | 11:06 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 999 | 0.69 | 1 | 3.9
BK BH 11 | 11:18 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 999 | -0.15 | 1 | 6.5
BK BH 12 | 11:22 | 0 | 1 | 20 | 79 | 0 | 0 | 999 | 0.24 | 1 | 6.6
BK BH 13 | 11:26 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 999 | -0.63 | 1 | 9.4
BK BH 14 | 11:29 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.21 | 1 | 3.5
BK BH 15 | 11:32 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 999 | 0.02 | 1 | 17.6
BK BH 16 | 11:35 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 999 | 0.58 | 1 | 11.4
BK BH 17 | 11:42 | 0.3 | 2 | 19.9 | 77.8 | 0 | 0 | 999 | 0.77 | 1 | 12.9
BK BH 18 | 10:08 | 0.3 | 2 | 19.8 | 77.9 | 0 | 0 | 999 | -0.96 | 6.8 | 21.2
BK BH 19 | 10:12 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | 0.38 | 1 | 11.2
BK BH 20 | 10:15 | 0.2 | 2 | 20 | 77.8 | 0 | 0 | 999 | -0.25 | 1 | 10.7
BK BH 21 | 10:20 | 0.2 | 1.8 | 19.9 | 78.1 | 0 | 0 | 999 | 0.14 | 1 | 21.7
BK BH 23 | 10:25 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 999 | 0.75 | 1 | 7.3
BK BH 24 | 10:28 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | -0.63 | 1 | 1.5
BK BH 25 | 10:32 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.14 | 1 | 9.9
Date | 2016-06-23
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:58 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1004 | -0.53 | 1 | 8.8
BK BH 3 | 11:03 | 0.2 | 1 | 19.6 | 79.2 | 0 | 0 | 1004 | 0.42 | 1 | 3.1
BK BH 4 | 11:04 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1004 | 0.52 | 1 | 5.1
BK BH 5 | 11:06 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1004 | 0.47 | 1 | 1.5
BK BH 6 | 11:10 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 1004 | -0.17 | 1 | 1.5
BK BH 7 | 11:14 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 1004 | 0.64 | 1 | 10
BK BH 8 | 11:17 | 29.1 | 1.1 | 20.1 | 49.7 | 0 | 0 | 1004 | 0.29 | 32.2 | 3.6
BK BH 9 | 11:23 | 26.7 | 1.2 | 19.4 | 52.7 | 0 | 0 | 1004 | -0.15 | 29.6 | 10.4
BK BH 10 | 11:28 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1004 | 0.36 | 1 | 3.9
BK BH 11 | 11:40 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1004 | -0.52 | 1 | 6.5
BK BH 12 | 11:44 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 1004 | 0.14 | 1 | 6.6
BK BH 13 | 11:48 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1004 | -0.78 | 1 | 9.4
BK BH 14 | 11:51 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1004 | 0.96 | 1 | 3.5
BK BH 15 | 11:54 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1004 | 0.32 | 1 | 17.6
BK BH 16 | 11:57 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1004 | -0.14 | 1 | 11.4
BK BH 17 | 12:04 | 0.4 | 1.8 | 20 | 77.8 | 0 | 0 | 1004 | 0.25 | 1 | 12.9
BK BH 18 | 10:30 | 0.2 | 1.9 | 19.9 | 78 | 0 | 0 | 1004 | -0.78 | 6.8 | 21.2
BK BH 19 | 10:34 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1004 | 0.63 | 1 | 11.2
BK BH 20 | 10:37 | 0.1 | 2.1 | 20.2 | 77.6 | 0 | 0 | 1004 | 0.87 | 1 | 10.7
BK BH 21 | 10:42 | 0.3 | 1.6 | 20.1 | 78 | 0 | 0 | 1004 | 0.25 | 1 | 21.7
BK BH 23 | 10:47 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1004 | -0.11 | 1 | 7.3
BK BH 24 | 10:50 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 1004 | 0.54 | 1 | 1.5
BK BH 25 | 10:54 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 1004 | 0.62 | 1 | 9.9
Date | 2016-06-30
Weather: | dry
Wind conditions: | Breezy
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:42 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1000 | 0.89 | 1 | 8.8
BK BH 3 | 10:47 | 0.3 | 1.1 | 19.5 | 79.1 | 0 | 0 | 1000 | -0.64 | 1 | 3.1
BK BH 4 | 10:49 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1000 | 0.52 | 1 | 5.1
BK BH 5 | 10:52 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 1000 | 0.78 | 1 | 1.5
BK BH 6 | 10:54 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1000 | 0.68 | 1 | 1.5
BK BH 7 | 10:58 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 1000 | 0.89 | 1 | 10
BK BH 8 | 11:01 | 28.9 | 1.4 | 19.9 | 49.8 | 0 | 0 | 1000 | 0.78 | 32.2 | 3.6
BK BH 9 | 11:07 | 26.9 | 1.9 | 19.6 | 51.6 | 0 | 0 | 1000 | 0.88 | 29.6 | 10.4
BK BH 10 | 11:12 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 1000 | 0.98 | 1 | 3.9
BK BH 11 | 11:14 | 0 | 1.3 | 20.1 | 78.6 | 0 | 0 | 1000 | -0.85 | 1 | 6.5
BK BH 12 | 11:28 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1000 | 0.58 | 1 | 6.6
BK BH 13 | 11:22 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1000 | -0.88 | 1 | 9.4
BK BH 14 | 11:35 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1000 | 0.62 | 1 | 3.5
BK BH 15 | 11:38 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1000 | 0.84 | 1 | 17.6
BK BH 16 | 11:41 | 0 | 1.9 | 20.1 | 78 | 0 | 0 | 1000 | 1.02 | 1 | 11.4
BK BH 17 | 11:48 | 0.3 | 2 | 19.9 | 77.8 | 0 | 0 | 1000 | 0.91 | 1 | 12.9
BK BH 18 | 10:14 | 0.1 | 3.2 | 20.1 | 76.6 | 0 | 0 | 1000 | 0.63 | 6.8 | 21.2
BK BH 19 | 10:18 | 0 | 3.1 | 19.9 | 77 | 0 | 0 | 1000 | 0.9 | 1 | 11.2
BK BH 20 | 10:21 | 0.2 | 2.6 | 19.9 | 77.3 | 0 | 0 | 1000 | 0.87 | 1 | 10.7
BK BH 21 | 10:26 | 0.4 | 1.4 | 20 | 78.2 | 0 | 0 | 1000 | 0.72 | 1 | 21.7
BK BH 23 | 10:31 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1000 | 0.82 | 1 | 7.3
BK BH 24 | 10:34 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1000 | -0.48 | 1 | 1.5
BK BH 25 | 10:38 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1000 | 0.93 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-06-29
Weather: |  | wet
Wind conditions: |  | Breezy
Air Temperature: |  | 15 | oC
Instrument: |  | GEM 2000 Plus | (with H2s filter fitted)
Serial No: |  | GM12289/10
Calibrated To: |  | 2016-09-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 14:00 | 44.3 | 34.1 | 0.8 | 20.8 | 4 | 0 | 985 | 156 |  | Egine running
GV1 |  | 24.6 | 22.6 | 2.3 | 50.5 | 3 | 0 | 985 | -1.23 |  | OFF
GV3 |  | 50.4 | 38.6 | 0.5 | 10.5 | 11 | 6 | 985 | -38.98 |  | Open Full
GV4 |  | 45.9 | 37.1 | 1.2 | 15.8 | 12 | 5 | 985 | -8.96 |  | Cracked Open
GV6 |  | 45 | 35 | 1.1 | 18.9 | 14 | 5 | 985 | -7.98 |  | Cracked Open
GV7 |  | 27.5 | 22.4 | 2 | 48.1 | 9 | 9 | 985 | -1.23 |  | Off Low Gas high o2
GV8 |  | 38.1 | 27 | 1.5 | 33.4 | 6 | 6 | 985 | -1 |  | Off Low Gas high o3
GV9 |  | 48 | 36.1 | 0.4 | 15.5 | 3 | 0 | 985 | -38.74 |  | Open Full
GV10 |  | 40.6 | 33.3 | 1.1 | 25 | 5 | 6 | 985 | -1 |  | Off
GV11 |  | 38.7 | 26.5 | 1.4 | 33.4 | 8 | 0 | 985 | -1.23 |  | Off
GV12+R3 Manifold |  | 50.1 | 34.5 | 0.4 | 15 | 7 | 0 | 985 | -38.56 |  | Open Full
GV12 |  | 50 | 35.8 | 0.5 | 13.7 | 9 | 0 | 985 | -38 |  | Open Full
R3 |  | 50.4 | 33.6 | 0.6 | 15.4 | 6 | 0 | 985 | -38.89 |  | Open Full
GV13 |  | 0.3 | 1.2 | 19.7 | 78.8 | 0 | 0 | 985 | -40.21 | -2.06 | Reg closed
GV14 |  | 47 | 37.9 | 0.2 | 14.9 | 7 | 0 | 985 | -39.23 |  | Open Full
GV15 |  | 52 | 39 | 0.3 | 8.7 | 12 | 0 | 985 | -39.47 |  | Open Full
GV16 |  | 53 | 40.2 | 0.2 | 6.6 | 3 | 0 | 985 | -0.02 | -12.58 | Reg cracked open
GV17+LC4 Manifold |  | 39.6 | 32.5 | 2.7 | 25.2 | 9 | 9 | 985 | -0.98 |  | Off at Manifold Gas drops quick.
GV17 |  | 39.2 | 32.1 | 2.5 | 26.2 | 11 | 11 | 985 | -1.06 |  | Open Full at Well
LC4 |  | 40 | 32.8 | 3 | 24.2 | 9 | 8 | 985 | -0.58 |  | Open Full at well
GV18 |  | 45 | 36.2 | 0.3 | 18.5 | 11 | 0 | 985 | -39.23 | -15.24 | reg closed to half way
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 37.8 | 32.4 | 2.6 | 27.2 | 6 | 12 | 985 | -1.09 |  | Off gas drops off quick.
GV23 |  | 50.1 | 36.2 | 0.5 | 13.2 | 6 | 0 | 985 | -39.63 |  | Open Full
GV24 |  | 52.9 | 37.8 | 0.6 | 8.7 | 8 | 0 | 985 | -38.78 |  | Open Full
GV25 |  | 39.6 | 35.2 | 0.5 | 24.7 | 11 | 0 | 985 | -35.26 | -1.23 | Reg Closed
GV26 + 27 Manifold |  | 50 | 37 | 0.5 | 12.5 | 9 | 3 | 985 | -38.56 |  | Open Full
GV28+ 29 Manifold |  | 49.9 | 36.8 | 0.6 | 12.7 | 7 | 3 | 985 | -39.04 |  | Open Full
GV26 |  | 50.4 | 37.2 | 0.3 | 12.1 | 8 | 5 | 985 | -39.23 |  | Open Full
GV27 |  | 48.2 | 37 | 0.6 | 14.2 | 6 | 4 | 985 | -39.12 |  | Open Full
GV28 |  | 50 | 37 | 0.5 | 12.5 | 8 | 2 | 985 | -38.47 |  | Open Full
GV29 |  | 49.5 | 35.9 | 0.7 | 13.9 | 9 | 0 | 985 | -39 |  | Open Full
GVA |  | 28.5 | 23.9 | 7.9 | 39.7 | 9 | 0 | 985 | -1.06 |  | Off Low gas
B+C Manifold |  | 48.2 | 36 | 0.6 | 15.2 | 14 | 1 | 985 | -38.99 |  | Open Full
GV B |  | 46.9 | 35.4 | 0.2 | 17.5 | 11 | 2 | 985 | -39.06 |  | Open Full
GV C |  | 48 | 35.9 | 0.3 | 15.8 | 13 | 0 | 985 | -39.96 |  | Open Full
GV30 |  | 45.6 | 36.3 | 1.3 | 16.8 | 11 | 4 | 985 | -18.52 | -11.23 | Reg closed to cracked
GV31 |  | 45 | 36.2 | 1.2 | 17.6 | 6 | 5 | 985 | -10.78 |  | Cracked Open
GV32 |  | 46.2 | 34.7 | 1 | 18.1 | 5 | 0 | 985 | -11.19 |  | Cracked Open
GV33 |  | 46.1 | 33.6 | 1 | 19.3 | 12 | 3 | 985 | -11.45 |  | Cracked Open
GV34 |  | 45 | 35.5 | 1.1 | 18.4 | 11 | 8 | 985 | -11.21 |  | Cracked Open
GV 35 (New Well) |  | 16.8 | 22.6 | 1.6 | 59 | 2 | 0 | 985 | -30.26 | -1.06 | Reg closed
GV 36 (New Well) |  | 14.8 | 18.6 | 3.7 | 62.9 | 6 | 0 | 985 | -0.99 |  | OFF low gas.
GV 37 (New Well) |  | 60.2 | 34.7 | 0 | 5.1 | 1 | 0 | 985 | -1 | -8.23 | Reg cracked open
GV 38 (New Well) |  | 49.2 | 31.7 | 0.8 | 18.3 | 3 | 0 | 985 | -10 | -17.89 | Cracked Open
GV 39 (New Well) |  | 47.1 | 30.6 | 1.8 | 20.5 | 2 | 0 | 985 | -14.23 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 44.5 | 36.2 | 1 | 18.3 | 6 | 3 | 985 | -14.23 |  | Cracked Open
GV 41 (New Well) |  | 45.6 | 35.6 | 1.2 | 17.6 | 3 | 0 | 985 | -11.23 |  | Cracked Open
GV 42 (New Well) |  | 37.8 | 33.6 | 1.5 | 27.1 | 11 | 6 | 985 | -1.45 |  | Off Low Gas
GV 43 (New Well) |  | 45.8 | 37.2 | 1.2 | 15.8 | 14 | 5 | 985 | -11.23 |  | Cracked open
GV 44 (New Well) |  | 40 | 32.6 | 0.9 | 26.5 | 13 | 0 | 985 | -1 |  | Off Low gas
GV 45 (New Well) |  | 46 | 38.2 | 1.1 | 14.7 | 11 | 0 | 985 | -11.23 |  | Cracked Open
GV 46 (New Well) |  | 48.2 | 38.6 | 0.3 | 12.9 | 10 | 0 | 985 | -38.79 |  | Open Full
GV 47 (New Well) |  | 45.9 | 37 | 1 | 16.1 | 8 | 3 | 985 | -12.39 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 38.9 | 0.3 | 0.8 | 9 | 5 | 985 | -37.81 |  | Open Full
GV 49 (New Well) |  | 46.2 | 32.8 | 1.1 | 19.9 | 7 | 4 | 985 | -12.56 |  | Cracked open
LC1B |  | 35.4 | 36 | 2.3 | 26.3 | 3 | 0 | 985 | -1.45 |  | OFF
LC2R? |  | 47.5 | 36.5 | 0.6 | 15.4 | 5 | 2 | 985 | -38.99 |  | Open Full
GV 2.1 |  | 47.9 | 37.5 | 0.4 | 14.2 | 8 | 3 | 985 | -39.13 |  | Open Full
GV 2.2+ LC2B MAN |  | 46.8 | 35.2 | 1.2 | 16.8 | 9 | 0 | 985 | -12.39 |  | Cracked Open at Manifold
GV 2.2 |  | 47 | 36 | 0.9 | 16.1 | 7 | 8 | 985 | -11.89 |  | Cracked Open
LC2B |  | 45.9 | 34.5 | 1.3 | 18.3 | 6 | 9 | 985 | -13.27 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 44.6 | 33.6 | 1.3 | 20.5 | 5 | 0 | 985 | -1.06 |  | Off
LC3.1 |  | 44.6 | 33.6 | 1.3 | 20.5 | 8 | 0 | 985 | -1.06 |  | Open At well
LC3 |  | 45.9 | 36.3 | 2.8 | 15 | 6 | 9 | 985 | -1.06 |  | OFF
LC4B |  | 22.8 | 24.4 | 3.6 | 49.2 | 9 | 0 | 985 | -8.09 | -1.23 | Reg Closed
R1 + R1B Manifold |  | 47.9 | 34.5 | 0.9 | 16.7 | 6 | 11 | 985 | -28.57 |  | Open Full
R1 |  | 44.9 | 33.6 | 1.2 | 20.3 | 6 | 9 | 985 | -9.25 |  | Cracked Open
R1B |  | 49.1 | 37.9 | 0.5 | 12.5 | 9 | 8 | 985 | -28.88 |  | Open Full
R2B |  | 50.2 | 37.1 | 0.4 | 12.3 | 8 | 5 | 985 | -28.57 |  | Open Full
R4B |  | 35.3 | 29.3 | 3.9 | 31.5 | 9 | 0 | 985 | -30.23 | -1.06 | Reg Closed
R6B |  | 50.1 | 32.5 | 0.3 | 17.1 | 9 | 8 | 985 | -28.77 |  | Open Full
LC5 |  | 47.5 | 31.7 | 2.2 | 18.6 | 5 | 7 | 985 | 0.56 |  | Left Off ( Gas drops quick)
LC6 |  | 45.6 | 32.9 | 2.5 | 19 | 7 | 10 | 985 | -0.25 |  | Left Off ( Gas drops quick)
LC6B |  | 50.2 | 37.1 | 0.6 | 12.1 | 10 | 7 | 985 | -28.57 |  | Open Full
PW1 |  | 0.8 | 0 | 17.9 | 81.3 | 12 | 8 | 985 | -1.25 |  | Left Off
PW2 |  | 34.9 | 17 | 3.9 | 44.2 | 9 | 9 | 985 | -0.89 |  | Left Off
PW3 |  | 31.8 | 20.8 | 5 | 42.4 | 5 | 10 | 985 | -1.25 |  | Left Off
PW4 |  | 46.1 | 34.5 | 1.2 | 18.2 | 7 | 7 | 985 | -7.58 |  | Cracked Open
PW5 |  | 23.6 | 21.7 | 1.2 | 53.5 | 11 | 9 | 985 | -1.23 |  | Left Off
PW6 |  | 28.7 | 23.9 | 2 | 45.4 | 8 | 11 | 985 | -1.09 |  | Left Off
Flare | 13:45 | 48.9 | 36.2 | 0.5 | 14.4 | 11 | 9 | 985 | 165 |  | Engine running 500 k/wh Gas improved o2 dropped
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## July
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-07-07
Weather: | dry
Wind conditions: | Breezy
Air Temperature: | 22 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0 | 1 | 20 | 79 | 0 | 0 | 998 | -0.21 | 1 | 8.8
BK BH 3 | 10:08 | 0.2 | 1.4 | 19.6 | 78.8 | 0 | 0 | 998 | 0.25 | 1 | 3.1
BK BH 4 | 10:11 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 998 | 0.23 | 1 | 5.1
BK BH 5 | 10:13 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 998 | -0.49 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 998 | -0.56 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 998 | 0.24 | 1 | 10
BK BH 8 | 10:22 | 28.3 | 1.2 | 19.8 | 50.7 | 0 | 0 | 998 | -0.11 | 32.2 | 3.6
BK BH 9 | 10:28 | 27.1 | 1.6 | 19.9 | 51.4 | 0 | 0 | 998 | -0.28 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 998 | -0.63 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 1 | 20 | 79 | 0 | 0 | 998 | 0.11 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 998 | 0.78 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 998 | -0.15 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 998 | 0.21 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 998 | -0.63 | 1 | 17.6
BK BH 16 | 11:02 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 998 | 0.21 | 1 | 11.4
BK BH 17 | 11:09 | 0.4 | 2.2 | 19.6 | 77.8 | 0 | 0 | 998 | -0.75 | 1 | 12.9
BK BH 18 | 9:35 | 0.2 | 3 | 20 | 76.8 | 0 | 0 | 998 | -0.63 | 6.8 | 21.2
BK BH 19 | 9:39 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 998 | 0.54 | 1 | 11.2
BK BH 20 | 9:42 | 0.1 | 2.4 | 19.8 | 77.7 | 0 | 0 | 998 | -0.96 | 1 | 10.7
BK BH 21 | 9:47 | 0.4 | 1.6 | 20 | 78 | 0 | 0 | 998 | -0.12 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 998 | 0.34 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 998 | -0.44 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 998 | 0.25 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-07-14
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:03 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1005 | -0.54 | 1 | 8.8
BK BH 3 | 10:08 | 0.2 | 1.5 | 19.9 | 78.4 | 0 | 0 | 1005 | 0.32 | 1 | 3.1
BK BH 4 | 10:10 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1005 | -0.32 | 1 | 5.1
BK BH 5 | 10:12 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1005 | 0.28 | 1 | 1.5
BK BH 6 | 10:15 | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1005 | 0.19 | 1 | 1.5
BK BH 7 | 10:19 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1005 | -0.65 | 1 | 10
BK BH 8 | 10:22 | 27.8 | 1.4 | 19.9 | 50.9 | 0 | 0 | 1005 | 0.34 | 32.2 | 3.6
BK BH 9 | 10:28 | 27.5 | 2.2 | 20 | 50.3 | 0 | 0 | 1005 | -0.11 | 29.6 | 10.4
BK BH 10 | 10:33 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1005 | 0.25 | 1 | 3.9
BK BH 11 | 10:45 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1005 | -0.37 | 1 | 6.5
BK BH 12 | 10:49 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 1005 | -0.87 | 1 | 6.6
BK BH 13 | 10:53 | 0 | 1.6 | 20.1 | 78.3 | 0 | 0 | 1005 | 0.69 | 1 | 9.4
BK BH 14 | 10:56 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1005 | -0.11 | 1 | 3.5
BK BH 15 | 10:59 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1005 | 0.23 | 1 | 17.6
BK BH 16 | 11:02 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1005 | -0.42 | 1 | 11.4
BK BH 17 | 11:09 | 0.2 | 2.6 | 19.8 | 77.4 | 0 | 0 | 1005 | 0.36 | 1 | 12.9
BK BH 18 | 9:35 | 0.3 | 3.2 | 19.6 | 76.9 | 0 | 0 | 1005 | -0.11 | 6.8 | 21.2
BK BH 19 | 9:39 | 0 | 4.2 | 19.9 | 75.9 | 0 | 0 | 1005 | -0.17 | 1 | 11.2
BK BH 20 | 9:42 | 0.2 | 2.9 | 20 | 76.9 | 0 | 0 | 1005 | 0.6 | 1 | 10.7
BK BH 21 | 9:47 | 0.3 | 1.1 | 19.8 | 78.8 | 0 | 0 | 1005 | 0.27 | 1 | 21.7
BK BH 23 | 9:52 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1005 | -0.14 | 1 | 7.3
BK BH 24 | 9:55 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 1005 | 0.25 | 1 | 1.5
BK BH 25 | 9:59 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1005 | -0.58 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-07-21
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:27 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 997 | -0.25 | 1 | 8.8
BK BH 3 | 10:32 | 0.3 | 1.2 | 19.9 | 78.6 | 0 | 0 | 997 | 0.49 | 1 | 3.1
BK BH 4 | 10:34 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 997 | 0.32 | 1 | 5.1
BK BH 5 | 10:36 | 0 | 0.7 | 19.5 | 79.8 | 0 | 0 | 997 | 0.19 | 1 | 1.5
BK BH 6 | 10:39 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 997 | 0.25 | 1 | 1.5
BK BH 7 | 10:43 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | 0.36 | 1 | 10
BK BH 8 | 10:46 | 28.1 | 1.6 | 19.6 | 50.7 | 0 | 0 | 997 | -0.01 | 32.2 | 3.6
BK BH 9 | 10:52 | 28 | 1.9 | 19.9 | 50.2 | 0 | 0 | 997 | 0.53 | 29.6 | 10.4
BK BH 10 | 10:57 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 997 | 0.24 | 1 | 3.9
BK BH 11 | 11:09 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 997 | -0.11 | 1 | 6.5
BK BH 12 | 11:13 | 0 | 2 | 20 | 78 | 0 | 0 | 997 | 0.56 | 1 | 6.6
BK BH 13 | 11:17 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 997 | 0.38 | 1 | 9.4
BK BH 14 | 11:20 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 997 | 0.14 | 1 | 3.5
BK BH 15 | 11:23 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 997 | 0.25 | 1 | 17.6
BK BH 16 | 11:26 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 997 | 0.36 | 1 | 11.4
BK BH 17 | 11:33 | 0.4 | 2.2 | 19.6 | 77.8 | 0 | 0 | 997 | -0.14 | 1 | 12.9
BK BH 18 | 9:59 | 0.3 | 3 | 19.7 | 77 | 0 | 0 | 997 | 0.36 | 6.8 | 21.2
BK BH 19 | 10:03 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 997 | -0.98 | 1 | 11.2
BK BH 20 | 10:06 | 0.1 | 2.5 | 19.8 | 77.6 | 0 | 0 | 997 | 0.75 | 1 | 10.7
BK BH 21 | 10:11 | 0.4 | 1.3 | 20 | 78.3 | 0 | 0 | 997 | -0.15 | 1 | 21.7
BK BH 23 | 10:16 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 997 | 0.36 | 1 | 7.3
BK BH 24 | 10:19 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 997 | -0.48 | 1 | 1.5
BK BH 25 | 10:23 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 997 | 0.21 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-07-28
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 20 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1002 | 0.69 | 1 | 8.8
BK BH 3 | 9:51 | 0.3 | 1.2 | 19.8 | 78.7 | 0 | 0 | 1002 | -0.55 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.32 | 1 | 5.1
BK BH 5 | 9:54 | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1002 | 0.54 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | 0.74 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1002 | 0.89 | 1 | 10
BK BH 8 | 10:05 | 27.5 | 1.1 | 20 | 51.4 | 0 | 0 | 1002 | 0.6 | 32.2 | 3.6
BK BH 9 | 10:11 | 27.9 | 2 | 20 | 50.1 | 0 | 0 | 1002 | 0.71 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1002 | 0.89 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1002 | -0.63 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | 0.46 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.78 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.4 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1002 | 0.63 | 1 | 17.6
BK BH 16 | 10:45 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1002 | 1.06 | 1 | 11.4
BK BH 17 | 10:52 | 0.1 | 2.7 | 19.5 | 77.7 | 0 | 0 | 1002 | 0.84 | 1 | 12.9
BK BH 18 | 9:18 | 0.4 | 3.5 | 19.5 | 76.6 | 0 | 0 | 1002 | 0.6 | 6.8 | 21.2
BK BH 19 | 9:22 | 0 | 4.2 | 19.8 | 76 | 0 | 0 | 1002 | 0.8 | 1 | 11.2
BK BH 20 | 9:25 | 0.2 | 2.8 | 19.6 | 77.4 | 0 | 0 | 1002 | 0.53 | 1 | 10.7
BK BH 21 | 9:30 | 0.4 | 1 | 19.6 | 79 | 0 | 0 | 1002 | 0.67 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 1002 | 0.89 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 1002 | -0.66 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 1002 | 0.74 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-07-27
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 18 | oC
Instrument: |  | GEM 2000 Plus | (with H2s filter fitted)
Serial No: |  | GM12289/10
Calibrated To: |  | 2016-09-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 13:30 | 46.9 | 33.6 | 0.6 | 18.9 | 3 | 1 | 996 | 165 |  | Egine running
GV1 |  | 27.9 | 23.9 | 2 | 46.2 | 4 | 0 | 996 | -0.59 |  | OFF
GV3 |  | 52.1 | 36.9 | 0.4 | 10.6 | 7 | 3 | 996 | -37 |  | Open Full
GV4 |  | 45.2 | 36.9 | 1.1 | 16.8 | 10 | 4 | 996 | -7.89 |  | Cracked Open
GV6 |  | 46.2 | 36.8 | 1.2 | 15.8 | 11 | 6 | 996 | -7.56 |  | Cracked Open
GV7 |  | 25.6 | 23.9 | 2.6 | 47.9 | 8 | 8 | 996 | -0.59 |  | Off Low Gas high o2
GV8 |  | 37.5 | 28.9 | 1.9 | 31.7 | 8 | 5 | 996 | -0.65 |  | Off Low Gas high o3
GV9 |  | 47.5 | 37.9 | 0.6 | 14 | 4 | 1 | 996 | -37.88 |  | Open Full
GV10 |  | 39.9 | 32.4 | 1.2 | 26.5 | 6 | 5 | 996 | -0.47 |  | Off
GV11 |  | 41.1 | 27 | 1.1 | 30.8 | 7 | 1 | 996 | -0.42 |  | Off
GV12+R3 Manifold |  | 49.9 | 33.6 | 0.5 | 16 | 8 | 0 | 996 | -37.02 |  | Open Full
GV12 |  | 49.5 | 33.4 | 0.5 | 16.6 | 10 | 1 | 996 | -37.36 |  | Open Full
R3 |  | 50.2 | 33.9 | 0.4 | 15.5 | 9 | 0 | 996 | -36.8 |  | Open Full
GV13 |  | 0.9 | 1.1 | 19.8 | 78.2 | 0 | 2 | 996 | -8.23 | -0.54 | Reg closed
GV14 |  | 48.2 | 38 | 0.3 | 13.5 | 8 | 0 | 996 | -37.06 |  | Open Full
GV15 |  | 51.5 | 38.9 | 0.4 | 9.2 | 11 | 3 | 996 | -37.42 |  | Open Full
GV16 |  | 47.1 | 36.5 | 1.1 | 15.3 | 5 | 0 | 996 | -8.96 |  | Left Cracked
GV17+LC4 Manifold |  | 41.2 | 33.3 | 2.6 | 22.9 | 8 | 8 | 996 | -0.56 |  | Off at Manifold Gas drops quick.
GV17 |  | 38.9 | 32.5 | 2.3 | 26.3 | 13 | 8 | 996 | -0.65 |  | Open Full at Well
LC4 |  | 42 | 33.9 | 3 | 21.1 | 8 | 8 | 996 | -0.44 |  | Open Full at well
GV18 |  | 50.1 | 37.9 | 0.2 | 11.8 | 12 | 0 | 996 | -14.56 | -37.85 | Reg Opened Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 38.9 | 33.4 | 2.7 | 25 | 8 | 13 | 996 | -0.45 |  | Off gas drops off quick.
GV23 |  | 49.9 | 36.8 | 0.4 | 12.9 | 9 | 0 | 996 | -37.47 |  | Open Full
GV24 |  | 48.7 | 35.6 | 0.3 | 15.4 | 7 | 0 | 996 | -37.93 |  | Open Full
GV25 |  | 41.2 | 33.8 | 0.6 | 24.4 | 7 | 0 | 996 | -0.63 |  | Left Closed
GV26 + 27 Manifold |  | 51.2 | 36.9 | 0.4 | 11.5 | 12 | 5 | 996 | -37.18 |  | Open Full
GV28+ 29 Manifold |  | 50.5 | 37 | 0.3 | 12.2 | 8 | 6 | 996 | -37.89 |  | Open Full
GV26 |  | 51.2 | 37.2 | 0.3 | 11.3 | 9 | 5 | 996 | -37.59 |  | Open Full
GV27 |  | 49.9 | 36.2 | 0.5 | 13.4 | 6 | 3 | 996 | -37.41 |  | Open Full
GV28 |  | 50.1 | 37.2 | 0.2 | 12.5 | 11 | 7 | 996 | -37.9 |  | Open Full
GV29 |  | 50.9 | 36.5 | 0.4 | 12.2 | 8 | 1 | 996 | -36.99 |  | Open Full
GVA |  | 27.9 | 24.5 | 7 | 40.6 | 5 | 0 | 996 | -0.62 |  | Off Low gas
B+C Manifold |  | 48.9 | 36.4 | 0.2 | 14.5 | 11 | 2 | 996 | -37.35 |  | Open Full
GV B |  | 47 | 35.9 | 0.4 | 16.7 | 10 | 3 | 996 | -38.02 |  | Open Full
GV C |  | 47.5 | 36.9 | 0.6 | 15 | 11 | 0 | 996 | -37.84 |  | Open Full
GV30 |  | 45 | 37 | 1.1 | 16.9 | 7 | 6 | 996 | -10.58 |  | Left Cracked
GV31 |  | 46.5 | 35.9 | 1 | 16.6 | 4 | 4 | 996 | -9.36 |  | Cracked Open
GV32 |  | 46.3 | 35 | 1.2 | 17.5 | 5 | 0 | 996 | -7.41 |  | Cracked Open
GV33 |  | 45.9 | 34.1 | 1.1 | 18.9 | 7 | 2 | 996 | -8.69 |  | Cracked Open
GV34 |  | 45.8 | 36.6 | 1.1 | 16.5 | 4 | 9 | 996 | -8.3 |  | Cracked Open
GV 35 (New Well) |  | 17.9 | 23.5 | 1.9 | 56.7 | 5 | 0 | 996 | -0.66 |  | Left Closed
GV 36 (New Well) |  | 15.9 | 19.9 | 3.9 | 60.3 | 5 | 1 | 996 | -0.68 |  | OFF low gas.
GV 37 (New Well) |  | 49.9 | 33.9 | 0.2 | 16 | 4 | 0 | 996 | -4.26 | -11.25 | Reg opened half way
GV 38 (New Well) |  | 47.9 | 33.6 | 1 | 17.5 | 8 | 1 | 996 | -8.36 |  | Cracked Open
GV 39 (New Well) |  | 46.9 | 32.8 | 1.5 | 18.8 | 6 | 0 | 996 | -8.01 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 46.1 | 35.9 | 1.1 | 16.9 | 3 | 2 | 996 | -7.89 |  | Cracked Open
GV 41 (New Well) |  | 45.8 | 36 | 1 | 17.2 | 4 | 0 | 996 | -8.92 |  | Cracked Open
GV 42 (New Well) |  | 39.9 | 34.9 | 1.4 | 23.8 | 12 | 5 | 996 | -0.68 |  | Off Low Gas
GV 43 (New Well) |  | 46 | 37.8 | 1.1 | 15.1 | 6 | 9 | 996 | -8.33 |  | Cracked open
GV 44 (New Well) |  | 42.5 | 33.9 | 1 | 22.6 | 7 | 0 | 996 | -0.63 |  | Off Low gas
GV 45 (New Well) |  | 46.5 | 38.9 | 1.1 | 13.5 | 6 | 0 | 996 | -7.88 |  | Cracked Open
GV 46 (New Well) |  | 49 | 38.9 | 0.4 | 11.7 | 2 | 1 | 996 | -37.89 |  | Open Full
GV 47 (New Well) |  | 46.2 | 36.8 | 1.1 | 15.9 | 8 | 5 | 996 | -8.96 |  | Cracked Opem
GV 48 (New Well) |  | 59.9 | 38 | 0.2 | 1.9 | 5 | 6 | 996 | -37 |  | Open Full
GV 49 (New Well) |  | 45.6 | 33.6 | 1.2 | 19.6 | 2 | 3 | 996 | -9.32 |  | Cracked open
LC1B |  | 36.9 | 35.9 | 2.5 | 24.7 | 2 | 0 | 996 | -0.61 |  | OFF
LC2R? |  | 47 | 37.1 | 0.8 | 15.1 | 4 | 3 | 996 | -37.56 |  | Open Full
GV 2.1 |  | 48.9 | 37.2 | 0.5 | 13.4 | 5 | 8 | 996 | -37.89 |  | Open Full
GV 2.2+ LC2B MAN |  | 46.2 | 34.9 | 1.1 | 17.8 | 6 | 0 | 996 | -8.96 |  | Cracked Open at Manifold
GV 2.2 |  | 46 | 34.9 | 1 | 18.1 | 5 | 8 | 996 | -8.8 |  | Cracked Open
LC2B |  | 46.9 | 35.2 | 1.2 | 16.7 | 2 | 9 | 996 | -9.04 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 46.9 | 34.9 | 1.4 | 16.8 | 3 | 1 | 996 | -0.54 |  | Off
LC3.1 |  | 46.9 | 34.9 | 1.4 | 16.8 | 6 | 1 | 996 | -1.06 |  | Open At well
LC3 |  | 45 | 36.1 | 2.5 | 16.4 | 8 | 3 | 996 | -0.35 |  | OFF
LC4B |  | 47.9 | 34.9 | 1.1 | 16.1 | 5 | 0 | 996 | -0.05 | -8.56 | Reg cracked open
R1 + R1B Manifold |  | 48 | 33.9 | 0.8 | 17.3 | 4 | 8 | 996 | -37.98 |  | Open Full
R1 |  | 46.9 | 33.2 | 1 | 18.9 | 7 | 12 | 996 | -8.05 |  | Cracked Open
R1B |  | 49.8 | 35.6 | 0.6 | 14 | 8 | 7 | 996 | -37.89 |  | Open Full
R2B |  | 49.8 | 35.9 | 0.3 | 14 | 7 | 7 | 996 | -37.24 |  | Open Full
R4B |  | 37.9 | 32.5 | 3.8 | 25.8 | 8 | 0 | 996 | -0.56 |  | Left closed
R6B |  | 50.6 | 35.9 | 0.4 | 13.1 | 6 | 8 | 996 | -37.01 |  | Open Full
LC5 |  | 45.9 | 32.8 | 2.5 | 18.8 | 5 | 9 | 996 | 0.66 |  | Left Off ( Gas drops quick)
LC6 |  | 43.9 | 34.9 | 2.1 | 19.1 | 3 | 10 | 996 | -0.45 |  | Left Off ( Gas drops quick)
LC6B |  | 51.4 | 36.9 | 0.5 | 11.2 | 9 | 9 | 996 | -37.55 |  | Open Full
PW1 |  | 1.2 | 0.2 | 15.9 | 82.7 | 14 | 6 | 996 | -0.56 |  | Left Off
PW2 |  | 32.9 | 18.8 | 4 | 44.3 | 10 | 8 | 996 | -0.89 |  | Left Off
PW3 |  | 33.6 | 19 | 4.2 | 43.2 | 6 | 5 | 996 | -0.47 |  | Left Off
PW4 |  | 47.2 | 35.8 | 1 | 16 | 8 | 4 | 996 | -5.25 |  | Cracked Open
PW5 |  | 25.4 | 22.3 | 1.5 | 50.8 | 10 | 5 | 996 | -0.36 |  | Left Off
PW6 |  | 29.9 | 25.4 | 2.4 | 42.3 | 7 | 10 | 996 | -0.47 |  | Left Off
Flare | 16:45 | 47 | 34.2 | 0.5 | 18.3 | 3 | 2 | 996 | 165 |  | Engine running 450 k/wh Gas improved o2 dropped
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## August
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-08-04
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.2 | 1.5 | 19.9 | 78.4 | 0 | 0 | 999 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:29 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 999 | 0.58 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 999 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 999 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.84 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 27.4 | 1.6 | 19.7 | 51.3 | 0 | 0 | 999 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:46 | 27.6 | 2.3 | 19.2 | 50.9 | 0 | 0 | 999 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 1.9 | 19.4 | 78.7 | 0 | 0 | 999 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 999 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 1.8 | 19.2 | 79 | 0 | 0 | 999 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:12 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 999 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | 0.41 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 999 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 999 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.2 | 2.4 | 20 | 77.4 | 0 | 0 | 999 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.3 | 3.2 | 19.8 | 76.7 | 0 | 0 | 999 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 4 | 20 | 76 | 0 | 0 | 999 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.4 | 3.1 | 20.1 | 76.4 | 0 | 0 | 999 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.2 | 1.4 | 19.9 | 78.5 | 0 | 0 | 999 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 999 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 999 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-08-11
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:52 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1001 | 0.61 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:57 | 0.1 | 2.1 | 19.8 | 78 | 0 | 0 | 1001 | -0.51 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:00 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 1001 | 0.41 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:02 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1001 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:04 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1001 | 0.62 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:08 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1001 | 0.62 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:11 | 27.8 | 1.4 | 19.4 | 51.4 | 0 | 0 | 1001 | 0.55 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:16 | 28 | 2 | 19.8 | 50.2 | 0 | 0 | 1001 | 0.63 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:22 | 0 | 1.5 | 19.3 | 79.2 | 0 | 0 | 1001 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:34 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1001 | -0.49 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:38 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1001 | 0.3 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:42 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1001 | -0.71 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:45 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 1001 | 0.4 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:48 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1001 | 0.44 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:51 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1001 | 0.81 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:58 | 0.3 | 2 | 20 | 77.7 | 0 | 0 | 1001 | 0.5 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:24 | 0.1 | 3 | 19.9 | 77 | 0 | 0 | 1001 | -0.53 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:28 | 0 | 4.3 | 19.8 | 75.9 | 0 | 0 | 1001 | 0.5 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:31 | 0.3 | 3.5 | 19.5 | 76.7 | 0 | 0 | 1001 | 0.59 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:26 | 0.2 | 1.9 | 20 | 77.9 | 0 | 0 | 1001 | 0.44 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:41 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1001 | 0.78 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:44 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1001 | -0.78 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:48 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1001 | 0.41 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-08-18
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:38 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 996 | -0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:43 | 0.3 | 2 | 19.7 | 78 | 0 | 0 | 996 | 0.85 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:45 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 996 | 0.75 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:48 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 996 | 0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:50 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 996 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:54 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 996 | -0.11 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:57 | 27.5 | 1.1 | 19.9 | 51.5 | 0 | 0 | 996 | 0.56 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:03 | 28.4 | 2.6 | 19.8 | 49.2 | 0 | 0 | 996 | 0.47 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:08 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 996 | -0.18 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:20 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 996 | 0.24 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:24 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 996 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:28 | 0 | 1.9 | 19.3 | 78.8 | 0 | 0 | 996 | 0.75 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:31 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 996 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:34 | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 996 | 0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:37 | 0 | 1.6 | 19.2 | 79.2 | 0 | 0 | 996 | 0.87 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:44 | 0.2 | 2.1 | 20 | 77.7 | 0 | 0 | 996 | 0.98 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:10 | 0.4 | 2.8 | 20.1 | 76.7 | 0 | 0 | 996 | -0.14 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:14 | 0 | 4 | 20 | 76 | 0 | 0 | 996 | 0.26 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:17 | 0.2 | 3.9 | 19.7 | 76.2 | 0 | 0 | 996 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:22 | 0.3 | 1.4 | 19.5 | 78.8 | 0 | 0 | 996 | -0.11 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:27 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 996 | 0.32 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:30 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 996 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:34 | 0 | 1 | 20 | 79 | 0 | 0 | 996 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-08-25
Weather: | dry
Wind conditions: | Breezy
Air Temperature: | 17 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:52 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 998 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:57 | 0.2 | 1.8 | 20 | 78 | 0 | 0 | 998 | 0.52 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:59 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 998 | 0.45 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 12:01 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 12:04 | 0 | 0.8 | 19.4 | 79.8 | 0 | 0 | 998 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 12:08 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 998 | 0.42 | 1 | 10 | 0.5 | 5
BK BH 8 | 12:11 | 27.9 | 1.4 | 20.1 | 50.6 | 0 | 0 | 998 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:17 | 28 | 2.5 | 19.8 | 49.7 | 0 | 0 | 998 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:22 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 998 | -0.14 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:34 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 998 | 0.75 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:38 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 998 | -0.63 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:42 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 998 | -0.25 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:45 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 998 | 0.24 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:48 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 998 | 0.69 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:51 | 0 | 1.7 | 20.1 | 78.2 | 0 | 0 | 998 | -0.15 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:58 | 0.3 | 2.4 | 20 | 77.3 | 0 | 0 | 998 | -0.42 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:24 | 0.4 | 2.5 | 19.8 | 77.3 | 0 | 0 | 998 | -0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:28 | 0 | 4.2 | 19.6 | 76.2 | 0 | 0 | 998 | 0.89 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:31 | 0.1 | 3.5 | 19.7 | 76.7 | 0 | 0 | 998 | -0.72 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:36 | 0.4 | 1.1 | 19.8 | 78.7 | 0 | 0 | 998 | 0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:41 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 998 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:44 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 998 | 0.74 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:48 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 998 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-08-17
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 19 | oC
Instrument: |  | GEM 2000 Plus | (with H2s filter fitted)
Serial No: |  | GM12289/10
Calibrated To: |  | 2016-09-22
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:30 | 47.5 | 35.6 | 0.7 | 16.2 | 7 | 2 | 1002 | 170 |  | Egine running
GV1 |  | 31.2 | 25.4 | 1.8 | 41.6 | 9 | 1 | 1002 | -0.87 |  | OFF
GV3 |  | 54.2 | 35.9 | 0.3 | 9.6 | 8 | 5 | 1002 | -37.46 |  | Open Full
GV4 |  | 45.8 | 36.5 | 1.1 | 16.6 | 16 | 9 | 1002 | -8 |  | Cracked Open
GV6 |  | 45.9 | 37 | 1.1 | 16 | 12 | 8 | 1002 | -8.36 |  | Cracked Open
GV7 |  | 27 | 25.4 | 2.7 | 44.9 | 11 | 5 | 1002 | -1.06 |  | Off Low Gas high o2
GV8 |  | 35.9 | 30 | 2.1 | 32 | 9 | 2 | 1002 | -1.07 |  | Off Low Gas high o3
GV9 |  | 48.5 | 36.9 | 0.5 | 14.1 | 7 | 7 | 1002 | -37.56 |  | Open Full
GV10 |  | 40.2 | 33.6 | 1.3 | 24.9 | 8 | 5 | 1002 | -0.36 |  | Off
GV11 |  | 42.2 | 28.4 | 1.1 | 28.3 | 9 | 8 | 1002 | -0.78 |  | Off
GV12+R3 Manifold |  | 49.9 | 34.7 | 0.4 | 15 | 6 | 6 | 1002 | -37.8 |  | Open Full
GV12 |  | 49.5 | 35.6 | 0.2 | 14.7 | 4 | 2 | 1002 | -37.52 |  | Open Full
R3 |  | 50.2 | 33.9 | 0.5 | 15.4 | 7 | 0 | 1002 | -37.99 |  | Open Full
GV13 |  | 1 | 1.5 | 19.2 | 78.3 | 8 | 6 | 1002 | -0.79 |  | Left Closed
GV14 |  | 49.9 | 37.4 | 0.2 | 12.5 | 8 | 3 | 1002 | -37.85 |  | Open Full
GV15 |  | 50.2 | 39.9 | 0.4 | 9.5 | 11 | 5 | 1002 | -37.54 |  | Open Full
GV16 |  | 47.5 | 37 | 1.2 | 14.3 | 9 | 8 | 1002 | -8 |  | Left Cracked
GV17+LC4 Manifold |  | 42.1 | 34 | 2.5 | 21.4 | 8 | 6 | 1002 | -0.89 |  | Off at Manifold Gas drops quick.
GV17 |  | 40 | 33.2 | 2.1 | 24.7 | 5 | 3 | 1002 | -0.78 |  | Open Full at Well
LC4 |  | 43.6 | 35 | 3.1 | 18.3 | 3 | 4 | 1002 | -0.98 |  | Open Full at well
GV18 |  | 51.2 | 38.9 | 0.3 | 9.6 | 0 | 5 | 1002 | -37.25 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 39.9 | 34.5 | 2.5 | 23.1 | 1 | 5 | 1002 | -0.87 |  | Off gas drops off quick.
GV23 |  | 50 | 37.8 | 0.5 | 11.7 | 7 | 0 | 1002 | -37.89 |  | Open Full
GV24 |  | 49.9 | 36.1 | 0.4 | 13.6 | 8 | 0 | 1002 | -38 |  | Open Full
GV25 |  | 40.7 | 34.2 | 0.9 | 24.2 | 9 | 2 | 1002 | -0.45 |  | Left Closed
GV26 + 27 Manifold |  | 50.2 | 37.5 | 0.3 | 12 | 8 | 5 | 1002 | -37.89 |  | Open Full
GV28+ 29 Manifold |  | 51 | 37.1 | 0.2 | 11.7 | 6 | 0 | 1002 | -37.55 |  | Open Full
GV26 |  | 50 | 37.1 | 0.3 | 12.6 | 8 | 4 | 1002 | -37.99 |  | Open Full
GV27 |  | 50.5 | 37.9 | 0.4 | 11.2 | 9 | 7 | 1002 | -37.57 |  | Open Full
GV28 |  | 51.2 | 36.8 | 0.2 | 11.8 | 5 | 8 | 1002 | -37.56 |  | Open Full
GV29 |  | 50.8 | 37.4 | 0.1 | 11.7 | 13 | 5 | 1002 | -37.48 |  | Open Full
GVA |  | 28.7 | 25.8 | 6.5 | 39 | 11 | 2 | 1002 | -0.89 |  | Off Low gas
B+C Manifold |  | 47.9 | 36.9 | 0.3 | 14.9 | 1 | 2 | 1002 | -37.35 |  | Open Full
GV B |  | 48.5 | 36.5 | 0.2 | 14.8 | 10 | 3 | 1002 | -37.89 |  | Open Full
GV C |  | 47 | 37 | 0.3 | 15.7 | 11 | 3 | 1002 | -37 |  | Open Full
GV30 |  | 45.8 | 37.2 | 1.1 | 15.9 | 2 | 3 | 1002 | -8.29 |  | Left Cracked
GV31 |  | 46 | 35.4 | 1.1 | 17.5 | 4 | 6 | 1002 | -8.56 |  | Cracked Open
GV32 |  | 46.1 | 36.1 | 1 | 16.8 | 5 | 8 | 1002 | -7.98 |  | Cracked Open
GV33 |  | 45.8 | 35.6 | 1 | 17.6 | 7 | 9 | 1002 | -9.06 |  | Cracked Open
GV34 |  | 46.9 | 37 | 1.2 | 14.9 | 7 | 8 | 1002 | -7.41 |  | Cracked Open
GV 35 (New Well) |  | 19.9 | 22.4 | 1.8 | 55.9 | 4 | 0 | 1002 | -0.89 |  | Left Closed
GV 36 (New Well) |  | 16.9 | 20 | 4 | 59.1 | 2 | 8 | 1002 | -0.41 |  | OFF low gas.
GV 37 (New Well) |  | 50 | 36.9 | 0.3 | 12.8 | 8 | 5 | 1002 | -11.59 | -37.89 | Reg Opened Full
GV 38 (New Well) |  | 46.2 | 32.9 | 1.1 | 19.8 | 5 | 7 | 1002 | -7.99 |  | Cracked Open
GV 39 (New Well) |  | 45.9 | 34.5 | 1.4 | 18.2 | 9 | 5 | 1002 | -8.25 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 46 | 36.9 | 1 | 16.1 | 6 | 0 | 1002 | -7.45 |  | Cracked Open
GV 41 (New Well) |  | 46.3 | 37 | 1 | 15.7 | 3 | 1 | 1002 | -8.69 |  | Cracked Open
GV 42 (New Well) |  | 40 | 33.9 | 1.5 | 24.6 | 11 | 4 | 1002 | -0.89 |  | Off Low Gas
GV 43 (New Well) |  | 46.2 | 38 | 1.2 | 14.6 | 4 | 9 | 1002 | -8.77 |  | Cracked open
GV 44 (New Well) |  | 41.9 | 34 | 1.1 | 23 | 1 | 1 | 1002 | -0.89 |  | Off Low gas
GV 45 (New Well) |  | 45.9 | 37.8 | 1 | 15.3 | 6 | 2 | 1002 | -8.21 |  | Cracked Open
GV 46 (New Well) |  | 48.5 | 38 | 0.2 | 13.3 | 7 | 5 | 1002 | -37.12 |  | Open Full
GV 47 (New Well) |  | 46 | 36.5 | 1.2 | 16.3 | 8 | 83 | 1002 | -9 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 39 | 0.3 | 0.7 | 6 | 5 | 1002 | -37.89 |  | Open Full
GV 49 (New Well) |  | 45.6 | 34.1 | 1.1 | 19.2 | 9 | 8 | 1002 | -8.41 |  | Cracked open
LC1B |  | 35.7 | 36 | 2.2 | 26.1 | 0 | 5 | 1002 | -0.55 |  | OFF
LC2R? |  | 48 | 37.9 | 0.6 | 13.5 | 11 | 2 | 1002 | -38 |  | Open Full
GV 2.1 |  | 49.2 | 37.5 | 0.4 | 12.9 | 12 | 0 | 1002 | -38.04 |  | Open Full
GV 2.2+ LC2B MAN |  | 46.5 | 35.2 | 1.1 | 17.2 | 5 | 4 | 1002 | -7.99 |  | Cracked Open at Manifold
GV 2.2 |  | 46.2 | 35.1 | 1.1 | 17.6 | 2 | 8 | 1002 | -7.87 |  | Cracked Open
LC2B |  | 46.8 | 35.2 | 1.2 | 16.8 | 2 | 7 | 1002 | -8.12 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47 | 35 | 1.1 | 16.9 | 5 | 5 | 1002 | -0.89 | -8.86 | Cracked open
LC3.1 |  | 47 | 35 | 1.1 | 16.9 | 5 | 5 | 1002 | -1.1 | -8.86 | Reg cracked Open
LC3 |  | 44.2 | 35.9 | 2.6 | 17.3 | 8 | 3 | 1002 | -0.35 |  | OFF
LC4B |  | 48 | 35.9 | 1.2 | 14.9 | 8 | 6 | 1002 | -8.86 |  | Left Cracked Open
R1 + R1B Manifold |  | 47.8 | 34.9 | 0.7 | 16.6 | 8 | 9 | 1002 | -37.11 |  | Open Full
R1 |  | 45.6 | 34 | 1 | 19.4 | 9 | 5 | 1002 | -8.06 |  | Cracked Open
R1B |  | 48.9 | 36 | 0.4 | 14.7 | 8 | 8 | 1002 | -37.88 |  | Open Full
R2B |  | 48.9 | 36 | 0.2 | 14.9 | 7 | 4 | 1002 | -37.08 |  | Open Full
R4B |  | 38 | 33.5 | 3.5 | 25 | 8 | 7 | 1002 | -0.89 |  | Left closed
R6B |  | 50.2 | 36.2 | 0.2 | 13.4 | 8 | 5 | 1002 | -37.46 |  | Open Full
LC5 |  | 44.2 | 33.8 | 2.9 | 19.1 | 6 | 2 | 1002 | 0.21 |  | Left Off ( Gas drops quick)
LC6 |  | 44.1 | 33.6 | 2.4 | 19.9 | 2 | 10 | 1002 | -0.08 |  | Left Off ( Gas drops quick)
LC6B |  | 52.2 | 37.9 | 0.3 | 9.6 | 5 | 4 | 1002 | -37.63 |  | Open Full
PW1 |  | 1.2 | 0.3 | 14.5 | 84 | 9 | 8 | 1002 | -0.58 |  | Left Off
PW2 |  | 33.6 | 20 | 3.9 | 42.5 | 10 | 5 | 1002 | -0.89 |  | Left Off
PW3 |  | 31.4 | 19.8 | 3.5 | 45.3 | 7 | 7 | 1002 | -0.14 |  | Left Off
PW4 |  | 45.9 | 34.7 | 1.1 | 18.3 | 1 | 4 | 1002 | -4.58 |  | Cracked Open
PW5 |  | 29.9 | 23.9 | 1.2 | 45 | 6 | 5 | 1002 | -0.36 |  | Left Off
PW6 |  | 30.3 | 24.4 | 2.1 | 43.2 | 8 | 6 | 1002 | -0.22 |  | Left Off
Flare | 16:00 | 47.7 | 35.9 | 0.6 | 15.8 | 6 | 3 | 1002 | 170 |  | Engine running 450 k/wh Gas improved o2 dropped
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## September
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-09-01
Weather: | dry
Wind conditions: | Breezy
Air Temperature: | 15 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:29 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 996 | -0.52 | 1 | 8.8
BK BH 3 | 11:34 | 0.3 | 1.6 | 19.6 | 78.5 | 0 | 0 | 996 | 0.71 | 1 | 3.1
BK BH 4 | 11:36 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 996 | 0.54 | 1 | 5.1
BK BH 5 | 11:39 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 996 | 0.32 | 1 | 1.5
BK BH 6 | 11:41 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 996 | 0.68 | 1 | 1.5
BK BH 7 | 11:45 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 996 | -0.29 | 1 | 10
BK BH 8 | 11:48 | 28.2 | 1.9 | 20 | 49.9 | 0 | 0 | 996 | 0.68 | 32.2 | 3.6
BK BH 9 | 11:54 | 27.8 | 2.4 | 19.4 | 50.4 | 0 | 0 | 996 | 0.42 | 29.6 | 10.4
BK BH 10 | 11:59 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 996 | 0.59 | 1 | 3.9
BK BH 11 | 12:11 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 996 | 0.24 | 1 | 6.5
BK BH 12 | 12:15 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 996 | -0.89 | 1 | 6.6
BK BH 13 | 12:19 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 996 | 0.52 | 1 | 9.4
BK BH 14 | 12:22 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 996 | 0.47 | 1 | 3.5
BK BH 15 | 12:25 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 996 | -0.18 | 1 | 17.6
BK BH 16 | 12:28 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 996 | 0.62 | 1 | 11.4
BK BH 17 | 12:35 | 0.2 | 3 | 19.8 | 77 | 0 | 0 | 996 | 0.47 | 1 | 12.9
BK BH 18 | 11:01 | 0.3 | 2.8 | 19.6 | 77.3 | 0 | 0 | 996 | -0.51 | 6.8 | 21.2
BK BH 19 | 11:05 | 0 | 4 | 19.5 | 76.5 | 0 | 0 | 996 | 0.12 | 1 | 11.2
BK BH 20 | 11:08 | 0.3 | 3.9 | 19.8 | 76 | 0 | 0 | 996 | 0.67 | 1 | 10.7
BK BH 21 | 11:13 | 0.3 | 1.2 | 19.9 | 78.6 | 0 | 0 | 996 | -0.35 | 1 | 21.7
BK BH 23 | 11:18 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 996 | 0.84 | 1 | 7.3
BK BH 24 | 11:21 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 996 | 0.38 | 1 | 1.5
BK BH 25 | 11:25 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 996 | -0.17 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-09-08
Weather: | dry
Wind conditions: | Breezy
Air Temperature: | 15 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:40 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 1004 | -0.52 | 1 | 8.8
BK BH 3 | 10:45 | 0.2 | 1.4 | 19.7 | 78.7 | 0 | 0 | 1004 | 0.26 | 1 | 3.1
BK BH 4 | 10:47 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1004 | -0.11 | 1 | 5.1
BK BH 5 | 10:50 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1004 | 0.35 | 1 | 1.5
BK BH 6 | 10:52 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1004 | 0.18 | 1 | 1.5
BK BH 7 | 10:56 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1004 | -0.26 | 1 | 10
BK BH 8 | 10:59 | 27.9 | 1.6 | 19.8 | 50.7 | 0 | 0 | 1004 | -0.36 | 32.2 | 3.6
BK BH 9 | 11:05 | 27.5 | 2.1 | 20 | 50.4 | 0 | 0 | 1004 | -0.5 | 29.6 | 10.4
BK BH 10 | 11:10 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1004 | -0.75 | 1 | 3.9
BK BH 11 | 11:22 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1004 | -0.23 | 1 | 6.5
BK BH 12 | 11:26 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1004 | 0.21 | 1 | 6.6
BK BH 13 | 11:30 | 0 | 2 | 20 | 78 | 0 | 0 | 1004 | 0.52 | 1 | 9.4
BK BH 14 | 11:33 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1004 | 0.75 | 1 | 3.5
BK BH 15 | 11:36 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1004 | 0.65 | 1 | 17.6
BK BH 16 | 11:39 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 1004 | -0.75 | 1 | 11.4
BK BH 17 | 11:46 | 0.1 | 2.8 | 20 | 77.1 | 0 | 0 | 1004 | 0.58 | 1 | 12.9
BK BH 18 | 10:12 | 0.2 | 2.4 | 19.8 | 77.6 | 0 | 0 | 1004 | 0.57 | 6.8 | 21.2
BK BH 19 | 10:16 | 0 | 4 | 19.5 | 76.5 | 0 | 0 | 1004 | -0.23 | 1 | 11.2
BK BH 20 | 10:19 | 0.4 | 3.5 | 19.5 | 76.6 | 0 | 0 | 1004 | 0.14 | 1 | 10.7
BK BH 21 | 10:24 | 0.1 | 1.4 | 20 | 78.5 | 0 | 0 | 1004 | -0.72 | 1 | 21.7
BK BH 23 | 10:29 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 1004 | 0.34 | 1 | 7.3
BK BH 24 | 10:32 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1004 | 0.68 | 1 | 1.5
BK BH 25 | 10:36 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1004 | 0.47 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-09-15
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 999 | 0.56 | 1 | 8.8
BK BH 3 | 10:24 | 0.3 | 1.1 | 19.9 | 78.7 | 0 | 0 | 999 | -0.62 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.52 | 1 | 5.1
BK BH 5 | 10:28 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 999 | -0.46 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 999 | 0.45 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 999 | 0.29 | 1 | 10
BK BH 8 | 10:38 | 27.5 | 1.4 | 19.5 | 51.6 | 0 | 0 | 999 | 0.47 | 32.2 | 3.6
BK BH 9 | 10:44 | 27.2 | 2 | 20 | 50.8 | 0 | 0 | 999 | 0.89 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.11 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 2.5 | 19.7 | 77.8 | 0 | 0 | 999 | -0.23 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 999 | 0.89 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 999 | -0.83 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 999 | 0.43 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 999 | 0.55 | 1 | 17.6
BK BH 16 | 11:18 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 999 | 0.56 | 1 | 11.4
BK BH 17 | 11:25 | 0.3 | 3.4 | 19.7 | 76.6 | 0 | 0 | 999 | 0.47 | 1 | 12.9
BK BH 18 | 9:51 | 0.3 | 2.9 | 20 | 76.8 | 0 | 0 | 999 | 0.54 | 6.8 | 21.2
BK BH 19 | 9:55 | 0 | 3.5 | 19.4 | 77.1 | 0 | 0 | 999 | 0.89 | 1 | 11.2
BK BH 20 | 9:58 | 0.2 | 3.2 | 19.6 | 77 | 0 | 0 | 999 | 0.55 | 1 | 10.7
BK BH 21 | 10:03 | 0.1 | 1.6 | 19.8 | 78.5 | 0 | 0 | 999 | 0.23 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 2.2 | 20.1 | 77.7 | 0 | 0 | 999 | 0.74 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 999 | 0.22 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 999 | 0.44 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-09-22
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 14 | OC
Instrument: | GEM 2000 Plus
Serial No: | GM12289/10
Calibrated To: | 2016-09-22
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1002 | 0.69 | 1 | 8.8
BK BH 3 | 9:51 | 0.2 | 1.2 | 19.5 | 79.1 | 0 | 0 | 1002 | -0.55 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.23 | 1 | 5.1
BK BH 5 | 9:55 | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 1002 | -0.14 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 1002 | 0.74 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.89 | 1 | 10
BK BH 8 | 10:05 | 27.4 | 1.5 | 20.1 | 51 | 0 | 0 | 1002 | 0.6 | 32.2 | 3.6
BK BH 9 | 10:11 | 28 | 2.1 | 20.1 | 49.8 | 0 | 0 | 1002 | 0.71 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1002 | 0.89 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1002 | -0.63 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | 0.46 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 1002 | -0.78 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1002 | 0.4 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.63 | 1 | 17.6
BK BH 16 | 10:45 | 0 | 1.8 | 19.4 | 78.8 | 0 | 0 | 1002 | 1.06 | 1 | 11.4
BK BH 17 | 10:52 | 0.4 | 3.6 | 19.9 | 76.1 | 0 | 0 | 1002 | 0.84 | 1 | 12.9
BK BH 18 | 9:18 | 0.2 | 2.5 | 20 | 77.3 | 0 | 0 | 1002 | 0.6 | 6.8 | 21.2
BK BH 19 | 9:22 | 0 | 3.1 | 19.6 | 77.3 | 0 | 0 | 1002 | 0.8 | 1 | 11.2
BK BH 20 | 9:25 | 0.1 | 3.5 | 19.9 | 76.5 | 0 | 0 | 1002 | 0.53 | 1 | 10.7
BK BH 21 | 9:30 | 0.3 | 1.8 | 20 | 77.9 | 0 | 0 | 1002 | 0.67 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1002 | 0.89 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1002 | -0.66 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1002 | 0.74 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-09-29
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GA 2000
Serial No: | GA10692
Calibrated To: | 2016-06-03
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:02 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 999 | 0.65 | 1 | 8.8
BK BH 3 | 10:07 | 0.3 | 1.5 | 19.4 | 78.8 | 0 | 0 | 999 | -0.48 | 1 | 3.1
BK BH 4 | 10:09 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | -0.23 | 1 | 5.1
BK BH 5 | 10:11 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 999 | 0.87 | 1 | 1.5
BK BH 6 | 10:14 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 999 | 0.72 | 1 | 1.5
BK BH 7 | 10:18 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 999 | 0.87 | 1 | 10
BK BH 8 | 10:21 | 28 | 1.6 | 19.7 | 50.7 | 0 | 0 | 999 | 0.63 | 32.2 | 3.6
BK BH 9 | 10:27 | 27.9 | 2.4 | 19.9 | 49.8 | 0 | 0 | 999 | 0.78 | 29.6 | 10.4
BK BH 10 | 10:32 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 999 | 0.71 | 1 | 3.9
BK BH 11 | 10:34 | 0 | 2.8 | 19.6 | 77.6 | 0 | 0 | 999 | -0.62 | 1 | 6.5
BK BH 12 | 10:48 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 999 | 0.47 | 1 | 6.6
BK BH 13 | 10:42 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 999 | -0.97 | 1 | 9.4
BK BH 14 | 10:55 | 0 | 2 | 20 | 78 | 0 | 0 | 999 | 0.48 | 1 | 3.5
BK BH 15 | 10:58 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 999 | 0.56 | 1 | 17.6
BK BH 16 | 11:01 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 999 | 1.27 | 1 | 11.4
BK BH 17 | 11:08 | 0.3 | 3 | 20 | 76.7 | 0 | 0 | 999 | 0.89 | 1 | 12.9
BK BH 18 | 9:34 | 0.1 | 2.2 | 19.8 | 77.9 | 0 | 0 | 999 | 0.59 | 6.8 | 21.2
BK BH 19 | 9:38 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 999 | 0.74 | 1 | 11.2
BK BH 20 | 9:41 | 0.3 | 3.9 | 20 | 75.8 | 0 | 0 | 999 | 0.5 | 1 | 10.7
BK BH 21 | 9:46 | 0.4 | 1.9 | 19.8 | 77.9 | 0 | 0 | 999 | 0.56 | 1 | 21.7
BK BH 23 | 9:51 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 999 | 0.85 | 1 | 7.3
BK BH 24 | 9:54 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 999 | -0.89 | 1 | 1.5
BK BH 25 | 9:58 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 999 | 0.62 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-09-14
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 15 | oC
Instrument: |  | GA 2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2016-06-03
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:15 | 48 | 36.5 | 0.5 | 15 | 6 | 9 | 999 | 165 |  | Egine running
GV1 |  | 32.8 | 25.9 | 1.6 | 39.7 | 8 | 2 | 999 | -0.87 |  | OFF
GV3 |  | 53.9 | 36.7 | 0.4 | 9 | 7 | 4 | 999 | -35.69 |  | Open Full
GV4 |  | 45.5 | 37 | 1 | 16.5 | 14 | 10 | 999 | -8.06 |  | Cracked Open
GV6 |  | 46 | 36.9 | 1.2 | 15.9 | 11 | 7 | 999 | -8.45 |  | Cracked Open
GV7 |  | 28.9 | 27 | 2.8 | 41.3 | 14 | 6 | 999 | -0.89 |  | Off Low Gas high o2
GV8 |  | 34.5 | 31.8 | 3 | 30.7 | 9 | 5 | 999 | -0.87 |  | Off Low Gas high o3
GV9 |  | 49 | 36.5 | 0.4 | 14.1 | 4 | 9 | 999 | -35.88 |  | Open Full
GV10 |  | 41 | 34.9 | 1.6 | 22.5 | 8 | 7 | 999 | -1.24 |  | Off
GV11 |  | 45.9 | 32.5 | 1 | 20.6 | 14 | 10 | 999 | -1 | -6.99 | Reg cracked open
GV12+R3 Manifold |  | 50.2 | 35.9 | 0.5 | 13.4 | 11 | 7 | 999 | -35.56 |  | Open Full
GV12 |  | 52.2 | 36.9 | 0.3 | 10.6 | 5 | 4 | 999 | -35.99 |  | Open Full
R3 |  | 48.9 | 34.2 | 0.6 | 16.3 | 6 | 0 | 999 | -35.14 |  | Open Full
GV13 |  | 1.5 | 2 | 19.5 | 77 | 8 | 9 | 999 | -0.58 |  | Left Closed
GV14 |  | 50.2 | 36.9 | 0.3 | 12.6 | 6 | 4 | 999 | -36 |  | Open Full
GV15 |  | 49.3 | 38.5 | 0.5 | 11.7 | 14 | 6 | 999 | -35.57 |  | Open Full
GV16 |  | 46.9 | 36.9 | 1.1 | 15.1 | 11 | 10 | 999 | -8.45 |  | Left Cracked
GV17+LC4 Manifold |  | 44.5 | 35.4 | 2.6 | 17.5 | 10 | 7 | 999 | -0.56 |  | Off at Manifold Gas drops quick.
GV17 |  | 42.6 | 34.9 | 2.2 | 20.3 | 9 | 4 | 999 | -0.56 |  | Open Full at Well
LC4 |  | 46.6 | 36 | 3 | 14.4 | 4 | 9 | 999 | -0.24 |  | Open Full at well
GV18 |  | 51.6 | 37.9 | 0.4 | 10.1 | 2 | 7 | 999 | -35.66 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 40.2 | 35.9 | 2.4 | 21.5 | 9 | 7 | 999 | -1.55 |  | Off gas drops off quick.
GV23 |  | 51.2 | 36.8 | 0.4 | 11.6 | 8 | 1 | 999 | -35.69 |  | Open Full
GV24 |  | 50.8 | 36.5 | 0.3 | 12.4 | 12 | 3 | 999 | -35.41 |  | Open Full
GV25 |  | 41 | 35.6 | 1.2 | 22.2 | 9 | 4 | 999 | -0.56 |  | Left Closed
GV26 + 27 Manifold |  | 50 | 37.5 | 0.2 | 12.3 | 8 | 6 | 999 | -35.99 |  | Open Full
GV28+ 29 Manifold |  | 50.9 | 36.9 | 0.3 | 11.9 | 8 | 2 | 999 | -36.21 |  | Open Full
GV26 |  | 50 | 37.2 | 0.1 | 12.7 | 8 | 3 | 999 | -36 |  | Open Full
GV27 |  | 50.2 | 37.8 | 0.3 | 11.7 | 6 | 8 | 999 | -35.89 |  | Open Full
GV28 |  | 51.3 | 36.5 | 0.2 | 12 | 6 | 10 | 999 | -35.74 |  | Open Full
GV29 |  | 50.6 | 37.1 | 0.4 | 11.9 | 15 | 6 | 999 | -36.55 |  | Open Full
GVA |  | 29.9 | 28.9 | 5.5 | 35.7 | 12 | 4 | 999 | -0.78 |  | Off Low gas
B+C Manifold |  | 48.8 | 37 | 0.2 | 14 | 9 | 9 | 999 | -35.55 |  | Open Full
GV B |  | 49 | 37.2 | 0.3 | 13.5 | 8 | 9 | 999 | -34.99 |  | Open Full
GV C |  | 47.6 | 36.8 | 0.1 | 15.5 | 8 | 8 | 999 | -36.02 |  | Open Full
GV30 |  | 46 | 36.9 | 1.2 | 15.9 | 76 | 7 | 999 | -8 |  | Left Cracked
GV31 |  | 45.9 | 36 | 1.1 | 17 | 8 | 5 | 999 | -7.89 |  | Cracked Open
GV32 |  | 45.7 | 35.4 | 1.2 | 17.7 | 9 | 6 | 999 | -8 |  | Cracked Open
GV33 |  | 45.9 | 35.9 | 1.1 | 17.1 | 8 | 8 | 999 | -7.89 |  | Cracked Open
GV34 |  | 44.9 | 36.5 | 1 | 17.6 | 12 | 8 | 999 | -7.84 |  | Cracked Open
GV 35 (New Well) |  | 20.1 | 23.9 | 1.9 | 54.1 | 14 | 7 | 999 | -1 |  | Left Closed
GV 36 (New Well) |  | 19 | 19.8 | 4.5 | 56.7 | 11 | 10 | 999 | -0.41 |  | OFF low gas.
GV 37 (New Well) |  | 51.2 | 37 | 0.4 | 11.4 | 10 | 6 | 999 | -35.87 |  | Left open Full
GV 38 (New Well) |  | 46 | 33.6 | 1.2 | 19.2 | 9 | 9 | 999 | -8.56 |  | Cracked Open
GV 39 (New Well) |  | 45.8 | 35.8 | 1.6 | 16.8 | 10 | 11 | 999 | -9 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 45.7 | 36 | 1.1 | 17.2 | 9 | 2 | 999 | -7.77 |  | Cracked Open
GV 41 (New Well) |  | 46 | 36.9 | 1 | 16.1 | 4 | 3 | 999 | -8.02 |  | Cracked Open
GV 42 (New Well) |  | 41.2 | 34.5 | 1.4 | 22.9 | 12 | 5 | 999 | -1 |  | Off Low Gas
GV 43 (New Well) |  | 46 | 38.1 | 1.3 | 14.6 | 5 | 11 | 999 | -8.99 |  | Cracked open
GV 44 (New Well) |  | 42.2 | 34.9 | 1.3 | 21.6 | 2 | 7 | 999 | -0.55 |  | Off Low gas
GV 45 (New Well) |  | 46.2 | 36.8 | 1 | 16 | 7 | 4 | 999 | -8.65 |  | Cracked Open
GV 46 (New Well) |  | 48 | 37.8 | 0.3 | 13.9 | 8 | 4 | 999 | -35.63 |  | Open Full
GV 47 (New Well) |  | 46.2 | 36.9 | 1.1 | 15.8 | 10 | 7 | 999 | -8.04 |  | Cracked Opem
GV 48 (New Well) |  | 60.1 | 39.5 | 0.5 | -0.1 | 7 | 9 | 999 | -35.87 |  | Open Full
GV 49 (New Well) |  | 46 | 35.9 | 1 | 17.1 | 10 | 12 | 999 | -8 |  | Cracked open
LC1B |  | 36 | 35.9 | 2.5 | 25.6 | 1 | 6 | 999 | -0.87 |  | OFF
LC2R? |  | 49.9 | 36.9 | 0.3 | 12.9 | 8 | 4 | 999 | -35.69 |  | Open Full
GV 2.1 |  | 48.6 | 37 | 0.1 | 14.3 | 5 | 0 | 999 | -35.89 |  | Open Full
GV 2.2+ LC2B MAN |  | 47 | 36 | 1.1 | 15.9 | 3 | 5 | 999 | -7.56 |  | Cracked Open at Manifold
GV 2.2 |  | 46.3 | 36.5 | 1.1 | 16.1 | 5 | 10 | 999 | -7.21 |  | Cracked Open
LC2B |  | 47.5 | 35.2 | 1.2 | 16.1 | 9 | 5 | 999 | -7.99 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.2 | 35.6 | 0.9 | 16.3 | 8 | 9 | 999 | -7.88 | -12.89 | Reg opened to half way
LC3.1 |  | 47.2 | 35.6 | 0.9 | 16.3 | 14 | 8 | 999 | -1.1 | -12.89 | opened half way
LC3 |  | 45 | 34 | 2.9 | 18.1 | 7 | 6 | 999 | -0.44 |  | OFF
LC4B |  | 48.2 | 36.2 | 1.3 | 14.3 | 8 | 8 | 999 | -8.12 |  | Left Cracked Open
R1 + R1B Manifold |  | 48 | 35.6 | 0.8 | 15.6 | 4 | 7 | 999 | -35.87 |  | Open Full
R1 |  | 46.5 | 34.4 | 1.1 | 18 | 7 | 9 | 999 | -8.12 |  | Cracked Open
R1B |  | 48.5 | 36.1 | 0.6 | 14.8 | 8 | 8 | 999 | -35.99 |  | Open Full
R2B |  | 49 | 37.5 | 0.4 | 13.1 | 9 | 8 | 999 | -35.78 |  | Open Full
R4B |  | 40.1 | 34.5 | 3.9 | 21.5 | 8 | 7 | 999 | -0.78 |  | Left closed
R6B |  | 50 | 36.8 | 0.3 | 12.9 | 8 | 6 | 999 | -36.06 |  | Open Full
LC5 |  | 45.2 | 35.9 | 3 | 15.9 | 4 | 5 | 999 | 0.45 |  | Left Off ( Gas drops quick)
LC6 |  | 46.9 | 34.5 | 2.9 | 15.7 | 4 | 11 | 999 | -0.58 |  | Left Off ( Gas drops quick)
LC6B |  | 51.2 | 36.1 | 0.4 | 12.3 | 6 | 10 | 999 | -35.19 |  | Open Full
PW1 |  | 1 | 0.2 | 15 | 83.8 | 5 | 9 | 999 | -0.59 |  | Left Off
PW2 |  | 32.9 | 19.4 | 3.5 | 44.2 | 5 | 8 | 999 | 0.78 |  | Left Off
PW3 |  | 32.7 | 19.1 | 3.2 | 45 | 7 | 910 | 999 | 0.45 |  | Left Off
PW4 |  | 45.9 | 35 | 1.2 | 17.9 | 8 | 11 | 999 | -5.89 |  | Cracked Open
PW5 |  | 31.9 | 24.8 | 1.1 | 42.2 | 9 | 12 | 999 | -0.56 |  | Left Off
PW6 |  | 31.2 | 25.8 | 2.4 | 40.6 | 8 | 7 | 999 | -0.47 |  | Left Off
Flare | 15:50 | 48.9 | 36.8 | 0.5 | 13.8 | 7 | 9 | 999 | 165 |  | Engine running 450 k/wh Gas improved o2 dropped
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## October
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-10-06
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:29 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 997 | -0.52 | 1 | 8.8
BK BH 3 | 11:34 | 0.2 | 1.2 | 19.1 | 79.5 | 0 | 0 | 997 | 0.71 | 1 | 3.1
BK BH 4 | 11:36 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 997 | 0.54 | 1 | 5.1
BK BH 5 | 11:39 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 997 | 0.32 | 1 | 1.5
BK BH 6 | 11:41 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 997 | 0.68 | 1 | 1.5
BK BH 7 | 11:45 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 997 | -0.29 | 1 | 10
BK BH 8 | 11:48 | 27.8 | 1.2 | 19.6 | 51.4 | 0 | 0 | 997 | 0.68 | 32.2 | 3.6
BK BH 9 | 11:54 | 28.1 | 2.1 | 20 | 49.8 | 0 | 0 | 997 | 0.42 | 29.6 | 10.4
BK BH 10 | 11:59 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 997 | 0.59 | 1 | 3.9
BK BH 11 | 12:11 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 997 | 0.24 | 1 | 6.5
BK BH 12 | 12:15 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 997 | -0.89 | 1 | 6.6
BK BH 13 | 12:19 | 0 | 2.6 | 19.3 | 78.1 | 0 | 0 | 997 | 0.52 | 1 | 9.4
BK BH 14 | 12:22 | 0 | 1.8 | 19.7 | 78.5 | 0 | 0 | 997 | 0.47 | 1 | 3.5
BK BH 15 | 12:25 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 997 | -0.18 | 1 | 17.6
BK BH 16 | 12:28 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 997 | 0.62 | 1 | 11.4
BK BH 17 | 12:35 | 0.2 | 2.8 | 20 | 77 | 0 | 0 | 997 | 0.47 | 1 | 12.9
BK BH 18 | 11:01 | 0.4 | 2.6 | 19.9 | 77.1 | 0 | 0 | 997 | -0.51 | 6.8 | 21.2
BK BH 19 | 11:05 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 997 | 0.12 | 1 | 11.2
BK BH 20 | 11:08 | 0.2 | 3.5 | 19.9 | 76.4 | 0 | 0 | 997 | 0.67 | 1 | 10.7
BK BH 21 | 11:13 | 0.1 | 1.6 | 20 | 78.3 | 0 | 0 | 997 | -0.35 | 1 | 21.7
BK BH 23 | 11:18 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 997 | 0.84 | 1 | 7.3
BK BH 24 | 11:21 | 0 | 0.8 | 19.2 | 80 | 0 | 0 | 997 | 0.38 | 1 | 1.5
BK BH 25 | 11:25 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 997 | -0.17 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-10-13
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 11:29 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1000 | -0.52 | 1 | 8.8
BK BH 3 | 11:34 | 0.1 | 1 | 19.6 | 79.3 | 0 | 0 | 1000 | 0.26 | 1 | 3.1
BK BH 4 | 11:36 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 1000 | -0.11 | 1 | 5.1
BK BH 5 | 11:39 | 0 | 0.4 | 20.1 | 79.5 | 0 | 0 | 1000 | 0.35 | 1 | 1.5
BK BH 6 | 11:41 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 1000 | 0.18 | 1 | 1.5
BK BH 7 | 11:45 | 0 | 1.6 | 19.4 | 79 | 0 | 0 | 1000 | -0.26 | 1 | 10
BK BH 8 | 11:48 | 27.6 | 1 | 19.3 | 52.1 | 0 | 0 | 1000 | -0.36 | 32.2 | 3.6
BK BH 9 | 11:54 | 28.4 | 2.3 | 20 | 49.3 | 0 | 0 | 1000 | -0.5 | 29.6 | 10.4
BK BH 10 | 11:59 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1000 | -0.75 | 1 | 3.9
BK BH 11 | 12:11 | 0 | 3 | 19.6 | 77.4 | 0 | 0 | 1000 | -0.23 | 1 | 6.5
BK BH 12 | 12:15 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1000 | 0.21 | 1 | 6.6
BK BH 13 | 12:19 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 1000 | 0.52 | 1 | 9.4
BK BH 14 | 12:22 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1000 | 0.75 | 1 | 3.5
BK BH 15 | 12:25 | 0 | 1.6 | 19.2 | 79.2 | 0 | 0 | 1000 | 0.65 | 1 | 17.6
BK BH 16 | 12:28 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1000 | -0.75 | 1 | 11.4
BK BH 17 | 12:35 | 0.3 | 2.9 | 19.8 | 77 | 0 | 0 | 1000 | 0.58 | 1 | 12.9
BK BH 18 | 11:01 | 0.1 | 2.7 | 19.6 | 77.6 | 0 | 0 | 1000 | 0.57 | 6.8 | 21.2
BK BH 19 | 11:05 | 0 | 3 | 19.9 | 77.1 | 0 | 0 | 1000 | -0.23 | 1 | 11.2
BK BH 20 | 11:08 | 0.4 | 3.6 | 20 | 76 | 0 | 0 | 1000 | 0.14 | 1 | 10.7
BK BH 21 | 11:13 | 0.2 | 1.5 | 19.5 | 78.8 | 0 | 0 | 1000 | -0.72 | 1 | 21.7
BK BH 23 | 11:18 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1000 | 0.34 | 1 | 7.3
BK BH 24 | 11:21 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 1000 | 0.68 | 1 | 1.5
BK BH 25 | 11:25 | 0 | 1.9 | 20.2 | 77.9 | 0 | 0 | 1000 | 0.47 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-10-20
Weather: | light rain
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 9:46 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 999 | 0.69 | 1 | 8.8
BK BH 3 | 9:51 | 0.2 | 1.2 | 20 | 78.6 | 0 | 0 | 999 | -0.55 | 1 | 3.1
BK BH 4 | 9:52 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 999 | 0.23 | 1 | 5.1
BK BH 5 | 9:55 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 999 | -0.14 | 1 | 1.5
BK BH 6 | 9:58 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 999 | 0.74 | 1 | 1.5
BK BH 7 | 10:02 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 999 | 0.89 | 1 | 10
BK BH 8 | 10:05 | 28 | 1.2 | 19.7 | 51.1 | 0 | 0 | 999 | 0.6 | 32.2 | 3.6
BK BH 9 | 10:11 | 28.1 | 2.1 | 19.9 | 49.9 | 0 | 0 | 999 | 0.71 | 29.6 | 10.4
BK BH 10 | 10:16 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 999 | 0.89 | 1 | 3.9
BK BH 11 | 10:28 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 999 | -0.63 | 1 | 6.5
BK BH 12 | 10:32 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 999 | 0.46 | 1 | 6.6
BK BH 13 | 10:36 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 999 | -0.78 | 1 | 9.4
BK BH 14 | 10:39 | 0 | 1.6 | 19 | 79.4 | 0 | 0 | 999 | 0.4 | 1 | 3.5
BK BH 15 | 10:42 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 999 | 0.63 | 1 | 17.6
BK BH 16 | 10:45 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 999 | 1.06 | 1 | 11.4
BK BH 17 | 10:52 | 0.2 | 2.1 | 19.6 | 78.1 | 0 | 0 | 999 | 0.84 | 1 | 12.9
BK BH 18 | 9:18 | 0.1 | 2.5 | 19.5 | 77.9 | 0 | 0 | 999 | 0.6 | 6.8 | 21.2
BK BH 19 | 9:22 | 0 | 2.6 | 19.3 | 78.1 | 0 | 0 | 999 | 0.8 | 1 | 11.2
BK BH 20 | 9:25 | 0.3 | 3.2 | 20 | 76.5 | 0 | 0 | 999 | 0.53 | 1 | 10.7
BK BH 21 | 9:30 | 0.1 | 1.4 | 19.6 | 78.9 | 0 | 0 | 999 | 0.67 | 1 | 21.7
BK BH 23 | 9:35 | 0 | 2 | 20 | 78 | 0 | 0 | 999 | 0.89 | 1 | 7.3
BK BH 24 | 9:38 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 999 | -0.66 | 1 | 1.5
BK BH 25 | 9:42 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | 0.74 | 1 | 9.9
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-10-27
Weather: | light rain
Wind conditions: | Calm
Air Temperature: | 7 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 | 10:19 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 996 | 0.75 | 1 | 8.8
BK BH 3 | 10:24 | 0.3 | 1.2 | 19.8 | 78.7 | 0 | 0 | 996 | -0.62 | 1 | 3.1
BK BH 4 | 10:25 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 996 | 0.52 | 1 | 5.1
BK BH 5 | 10:28 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 996 | -0.21 | 1 | 1.5
BK BH 6 | 10:31 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 996 | 0.84 | 1 | 1.5
BK BH 7 | 10:35 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 996 | 0.96 | 1 | 10
BK BH 8 | 10:38 | 28.2 | 1.2 | 19.6 | 51 | 0 | 0 | 996 | 0.74 | 32.2 | 3.6
BK BH 9 | 10:44 | 27.8 | 2.1 | 20 | 50.1 | 0 | 0 | 996 | 0.79 | 29.6 | 10.4
BK BH 10 | 10:49 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 996 | 0.98 | 1 | 3.9
BK BH 11 | 11:01 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 996 | -0.78 | 1 | 6.5
BK BH 12 | 11:05 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 996 | 0.52 | 1 | 6.6
BK BH 13 | 11:09 | 0 | 2 | 20 | 78 | 0 | 0 | 996 | -0.83 | 1 | 9.4
BK BH 14 | 11:12 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 996 | 0.43 | 1 | 3.5
BK BH 15 | 11:15 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 996 | 0.71 | 1 | 17.6
BK BH 16 | 11:18 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 996 | 1.08 | 1 | 11.4
BK BH 17 | 11:25 | 0.3 | 2.1 | 20 | 77.6 | 0 | 0 | 996 | 0.93 | 1 | 12.9
BK BH 18 | 9:51 | 0.2 | 2.5 | 19.2 | 78.1 | 0 | 0 | 996 | 0.54 | 6.8 | 21.2
BK BH 19 | 9:55 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 996 | 0.89 | 1 | 11.2
BK BH 20 | 9:58 | 0.2 | 3.2 | 19.9 | 76.7 | 0 | 0 | 996 | 0.67 | 1 | 10.7
BK BH 21 | 10:03 | 0.1 | 1.4 | 19.4 | 79.1 | 0 | 0 | 996 | 0.61 | 1 | 21.7
BK BH 23 | 10:08 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 996 | 0.74 | 1 | 7.3
BK BH 24 | 10:11 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 996 | -0.62 | 1 | 1.5
BK BH 25 | 10:15 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 996 | 0.87 | 1 | 9.9
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-10-12
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 15 | oC
Instrument: |  | GA 2000 | (with H2s filter fitted)
Serial No: |  | GA10692
Calibrated To: |  | 2016-06-03
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:15 | 51.2 | 38.9 | 0.4 | 9.5 | 10 | 7 | 1002 | 165 |  | Egine running
GV1 |  | 34 | 27.9 | 1.2 | 36.9 | 9 | 6 | 1002 | -0.56 |  | OFF
GV3 |  | 52.6 | 35.9 | 0.2 | 11.3 | 8 | 3 | 1002 | -33.96 |  | Open Full
GV4 |  | 46 | 35.6 | 1.1 | 17.3 | 11 | 9 | 1002 | -7.99 |  | Cracked Open
GV6 |  | 45.1 | 35.2 | 1 | 18.7 | 12 | 8 | 1002 | -8.06 |  | Cracked Open
GV7 |  | 30 | 27.9 | 2.5 | 39.6 | 9 | 6 | 1002 | -0.45 |  | Off Low Gas high o2
GV8 |  | 35.9 | 32 | 2.4 | 29.7 | 8 | 8 | 1002 | -0.63 |  | Off Low Gas high o3
GV9 |  | 49.2 | 37.5 | 0.5 | 12.8 | 8 | 7 | 1002 | -34 |  | Open Full
GV10 |  | 42.1 | 35.2 | 1.2 | 21.5 | 17 | 8 | 1002 | -1.06 |  | Off
GV11 |  | 44.7 | 33.6 | 1.1 | 20.6 | 7 | 11 | 1002 | -7.55 |  | Cracked Open
GV12+R3 Manifold |  | 51 | 36 | 0.6 | 12.4 | 9 | 9 | 1002 | -34.52 |  | Open Full
GV12 |  | 51.4 | 36.8 | 0.4 | 11.4 | 9 | 9 | 1002 | -34.21 |  | Open Full
R3 |  | 49.6 | 35.2 | 0.7 | 14.5 | 8 | 8 | 1002 | -34.21 |  | Open Full
GV13 |  | 1.9 | 2.4 | 19.1 | 76.6 | 13 | 6 | 1002 | -0.26 |  | Left Closed
GV14 |  | 50 | 37.4 | 0.4 | 12.2 | 10 | 8 | 1002 | -34.21 |  | Open Full
GV15 |  | 49.6 | 37.9 | 0.6 | 11.9 | 911 | 9 | 1002 | -35 |  | Open Full
GV16 |  | 45.2 | 37 | 1 | 16.8 | 8 | 12 | 1002 | -8.09 |  | Left Cracked
GV17+LC4 Manifold |  | 45 | 35.4 | 2.6 | 17 | 6 | 8 | 1002 | -0.45 |  | Off at Manifold Gas drops quick.
GV17 |  | 43.9 | 34.9 | 2.1 | 19.1 | 6 | 6 | 1002 | -0.36 |  | Open Full at Well
LC4 |  | 46.5 | 36 | 2.9 | 14.6 | 5 | 10 | 1002 | -0.52 |  | Open Full at well
GV18 |  | 50.4 | 38 | 0.5 | 11.1 | 3 | 8 | 1002 | -33.98 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 42.1 | 36 | 2.5 | 19.4 | 8 | 9 | 1002 | -1.09 |  | Off gas drops off quick.
GV23 |  | 50.2 | 37 | 0.5 | 12.3 | 7 | 9 | 1002 | -34 |  | Open Full
GV24 |  | 51.6 | 36.2 | 0.3 | 11.9 | 9 | 8 | 1002 | -34.56 |  | Open Full
GV25 |  | 42.9 | 36 | 1.3 | 19.8 | 8 | 6 | 1002 | -0.66 |  | Left Closed
GV26 + 27 Manifold |  | 51.2 | 36.9 | 0.3 | 11.6 | 9 | 8 | 1002 | -34.21 |  | Open Full
GV28+ 29 Manifold |  | 50.6 | 37 | 0.2 | 12.2 | 10 | 8 | 1002 | -33.98 |  | Open Full
GV26 |  | 50.4 | 36.7 | 0.1 | 12.8 | 9 | 7 | 1002 | -34.55 |  | Open Full
GV27 |  | 51.9 | 37.5 | 0.4 | 10.2 | 9 | 8 | 1002 | -34.21 |  | Open Full
GV28 |  | 51 | 36.4 | 0.1 | 12.5 | 8 | 9 | 1002 | -34.17 |  | Open Full
GV29 |  | 50.2 | 37 | 0.3 | 12.5 | 12 | 8 | 1002 | -34.93 |  | Open Full
GVA |  | 32.9 | 27.5 | 5.2 | 34.4 | 11 | 7 | 1002 | -0.81 |  | Off Low gas
B+C Manifold |  | 49 | 36.8 | 0.3 | 13.9 | 9 | 11 | 1002 | -34.21 |  | Open Full
GV B |  | 49.6 | 37.1 | 0.2 | 13.1 | 9 | 12 | 1002 | -33.89 |  | Open Full
GV C |  | 48.2 | 36.9 | 0.4 | 14.5 | 9 | 10 | 1002 | -34.59 |  | Open Full
GV30 |  | 46.8 | 35.4 | 1.3 | 16.5 | 16 | 9 | 1002 | -8.04 |  | Left Cracked
GV31 |  | 45 | 35.9 | 1 | 18.1 | 10 | 14 | 1002 | -7.45 |  | Cracked Open
GV32 |  | 44.9 | 34.9 | 1.1 | 19.1 | 11 | 6 | 1002 | -7.86 |  | Cracked Open
GV33 |  | 45.2 | 36.9 | 1.2 | 16.7 | 7 | 3 | 1002 | -8.09 |  | Cracked Open
GV34 |  | 44.8 | 37 | 1 | 17.2 | 8 | 9 | 1002 | -8.01 |  | Cracked Open
GV 35 (New Well) |  | 19.9 | 22.6 | 1.8 | 55.7 | 6 | 8 | 1002 | -0.99 |  | Left Closed
GV 36 (New Well) |  | 20.4 | 20.4 | 4.9 | 54.3 | 6 | 9 | 1002 | -0.41 |  | OFF low gas.
GV 37 (New Well) |  | 50.3 | 36.9 | 0.2 | 12.6 | 5 | 8 | 1002 | -34.09 |  | Left open Full
GV 38 (New Well) |  | 45.8 | 34.8 | 1.3 | 18.1 | 12 | 9 | 1002 | -8.51 |  | Cracked Open
GV 39 (New Well) |  | 46.2 | 37.2 | 1.5 | 15.1 | 10 | 8 | 1002 | -7.96 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 46.2 | 37 | 1 | 15.8 | 11 | 7 | 1002 | -8.17 |  | Cracked Open
GV 41 (New Well) |  | 46.1 | 36.9 | 1.2 | 15.8 | 3 | 4 | 1002 | -8.11 |  | Cracked Open
GV 42 (New Well) |  | 42.6 | 35.6 | 1.2 | 20.6 | 6 | 6 | 1002 | -1.06 |  | Off Low Gas
GV 43 (New Well) |  | 46.8 | 36.9 | 1.1 | 15.2 | 3 | 11 | 1002 | -8.34 |  | Cracked open
GV 44 (New Well) |  | 41 | 35.6 | 1.2 | 22.2 | 3 | 6 | 1002 | -0.55 |  | Off Low gas
GV 45 (New Well) |  | 46.8 | 37 | 1.2 | 15 | 8 | 9 | 1002 | -8.09 |  | Cracked Open
GV 46 (New Well) |  | 48.2 | 38.9 | 0.4 | 12.5 | 10 | 9 | 1002 | -33.99 |  | Open Full
GV 47 (New Well) |  | 46.9 | 37 | 1 | 15.1 | 11 | 6 | 1002 | -7.89 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 8 | 8 | 1002 | -34.25 |  | Open Full
GV 49 (New Well) |  | 45.5 | 34.9 | 1.1 | 18.5 | 12 | 9 | 1002 | -7.99 |  | Cracked open
LC1B |  | 35.9 | 35.4 | 2.2 | 26.5 | 11 | 7 | 1002 | -0.98 |  | OFF
LC2R? |  | 50 | 37.4 | 0.2 | 12.4 | 9 | 7 | 1002 | -34.12 |  | Open Full
GV 2.1 |  | 49.2 | 38.9 | 0.2 | 11.7 | 6 | 0 | 1002 | -24.59 |  | Open Full
GV 2.2+ LC2B MAN |  | 48.2 | 35.9 | 1.2 | 14.7 | 10 | 10 | 1002 | -8 |  | Cracked Open at Manifold
GV 2.2 |  | 47.5 | 36.4 | 1.1 | 15 | 8 | 9 | 1002 | -7.89 |  | Cracked Open
LC2B |  | 48.5 | 35.6 | 1.4 | 14.5 | 12 | 3 | 1002 | -8.23 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.1 | 36 | 0.8 | 16.1 | 11 | 8 | 1002 | -15.29 |  | Left Open Half Way
LC3.1 |  | 47.1 | 36 | 0.8 | 16.1 | 11 | 8 | 1002 | -15.29 |  | Left open half way
LC3 |  | 46 | 33.9 | 2.5 | 17.6 | 8 | 10 | 1002 | -0.56 |  | OFF
LC4B |  | 48.5 | 37 | 1.2 | 13.3 | 18 | 9 | 1002 | -7.99 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.2 | 36 | 0.6 | 15.2 | 8 | 11 | 1002 | -34.57 |  | Open Full
R1 |  | 46 | 35 | 1.2 | 17.8 | 4 | 12 | 1002 | -8.19 |  | Cracked Open
R1B |  | 48.6 | 37.5 | 0.4 | 13.5 | 7 | 14 | 1002 | -8.99 |  | Open Full
R2B |  | 49.2 | 38 | 0.6 | 12.2 | 8 | 18 | 1002 | -7.54 |  | Open Full
R4B |  | 42 | 35.2 | 3.8 | 19 | 9 | 2 | 1002 | -0.89 |  | Left closed
R6B |  | 51.2 | 37.9 | 0.5 | 10.4 | 8 | 6 | 1002 | -34.57 |  | Open Full
LC5 |  | 46 | 36.2 | 3.2 | 14.6 | 7 | 9 | 1002 | 0.51 |  | Left Off ( Gas drops quick)
LC6 |  | 47.2 | 35 | 2.5 | 15.3 | 8 | 7 | 1002 | -0.69 |  | Left Off ( Gas drops quick)
LC6B |  | 50.8 | 36.5 | 0.6 | 12.1 | 9 | 8 | 1002 | -34.21 |  | Open Full
PW1 |  | 1.2 | 0.3 | 14 | 84.5 | 9 | 12 | 1002 | -0.69 |  | Left Off
PW2 |  | 33.6 | 18.6 | 3.2 | 44.6 | 8 | 9 | 1002 | 0 |  | Left Off
PW3 |  | 34.9 | 20 | 2.9 | 42.2 | 5 | 10 | 1002 | 0.32 |  | Left Off
PW4 |  | 46 | 36.5 | 1.1 | 16.4 | 5 | 12 | 1002 | -6.58 |  | Cracked Open
PW5 |  | 32.5 | 25.1 | 1.6 | 40.8 | 10 | 13 | 1002 | -0.89 |  | Left Off
PW6 |  | 33.9 | 26.9 | 2.5 | 36.7 | 9 | 8 | 1002 | -0.78 |  | Left Off
Flare | 15:50 | 51.1 | 38.9 | 0.4 | 9.6 | 9 | 7 | 1002 | 165 |  | Engine running 350 k/wh
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.

## November
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-11-03
Weather: | light rain
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:15 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 997 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:20 | 0.2 | 1.3 | 20 | 78.5 | 0 | 0 | 997 | -0.36 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:23 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 997 | -0.78 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:25 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 997 | -0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:27 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 997 | 0.95 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:31 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 997 | -0.63 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:34 | 28.9 | 1.4 | 19.6 | 50.1 | 0 | 0 | 997 | 0.25 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:40 | 28 | 1.5 | 20.1 | 50.4 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:45 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 997 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:57 | 0 | 2.6 | 20.1 | 77.3 | 0 | 0 | 997 | -0.65 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:01 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 997 | 0.32 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:05 | 0 | 2.2 | 19.5 | 78.3 | 0 | 0 | 997 | -0.17 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:08 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 997 | 0.36 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:11 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 997 | -0.98 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:14 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 997 | 0.25 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:21 | 0.4 | 2.4 | 19.7 | 77.5 | 0 | 0 | 997 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:47 | 0.1 | 2 | 19.5 | 78.4 | 0 | 0 | 997 | 0.75 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:51 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 997 | 0.36 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:54 | 0.3 | 3 | 20 | 76.7 | 0 | 0 | 997 | -0.82 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:59 | 0.2 | 1.6 | 19.6 | 78.6 | 0 | 0 | 997 | 0.39 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:04 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:07 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 997 | 0.27 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:11 | 0 | 1.8 | 19.4 | 78.8 | 0 | 0 | 997 | -0.54 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-11-10
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 8 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:36 | 0 | 3 | 19.6 | 77.4 | 0 | 0 | 995 | -0.63 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:41 | 0.3 | 1.4 | 19.8 | 78.5 | 0 | 0 | 995 | -0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:43 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 995 | -0.45 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:46 | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 995 | -0.28 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:48 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 995 | -0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:52 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 995 | 0.35 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:55 | 28.6 | 1.5 | 19.5 | 50.4 | 0 | 0 | 995 | -0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:01 | 28.2 | 1.2 | 20 | 50.6 | 0 | 0 | 995 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:06 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 995 | 0.38 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:18 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 995 | -0.96 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:22 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 995 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:26 | 0 | 2.3 | 19.7 | 78 | 0 | 0 | 995 | 0.24 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:29 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 995 | -0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:32 | 0 | 2 | 20.1 | 77.9 | 0 | 0 | 995 | 0.38 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:35 | 0 | 2.1 | 19.2 | 78.7 | 0 | 0 | 995 | -0.77 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:42 | 0.3 | 2.9 | 19.9 | 76.9 | 0 | 0 | 995 | -0.65 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:08 | 0.2 | 2.3 | 19.8 | 77.7 | 0 | 0 | 995 | -78 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:12 | 0 | 1.8 | 19.6 | 78.6 | 0 | 0 | 995 | 0.63 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:15 | 0.4 | 2.4 | 20 | 77.2 | 0 | 0 | 995 | -0.87 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:20 | 0.1 | 1.9 | 19.9 | 78.1 | 0 | 0 | 995 | -0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:25 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 995 | -0.48 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:28 | 0 | 0.6 | 20.2 | 79.2 | 0 | 0 | 995 | -0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:32 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 995 | 0.86 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-11-17
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 6 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:58 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 999 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:03 | 0.2 | 1.3 | 19.5 | 79 | 0 | 0 | 999 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:05 | 0 | 1 | 19.3 | 79.7 | 0 | 0 | 999 | -0.46 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:07 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 999 | -0.31 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:10 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 999 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:14 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:17 | 28.4 | 1.5 | 19.8 | 50.3 | 0 | 0 | 999 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:23 | 28 | 1.5 | 19.6 | 50.9 | 0 | 0 | 999 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:28 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 999 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:40 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 999 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:44 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 999 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:48 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 999 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:51 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 999 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:54 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 999 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:57 | 0 | 2.6 | 19.5 | 77.9 | 0 | 0 | 999 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:04 | 0.2 | 3 | 19.6 | 77.2 | 0 | 0 | 999 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:30 | 0.3 | 2.6 | 19.5 | 77.6 | 0 | 0 | 999 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:34 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 999 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:37 | 0.3 | 2.6 | 19.9 | 77.2 | 0 | 0 | 999 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:42 | 0.2 | 1.5 | 19.8 | 78.5 | 0 | 0 | 999 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:47 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 999 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:50 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:54 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 999 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-11-24
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 5 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:23 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1002 | 0.42 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:28 | 0.3 | 1.4 | 20 | 78.3 | 0 | 0 | 1002 | 0.75 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:30 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1002 | 0.12 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 1002 | 0.29 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:35 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1002 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:39 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.14 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:42 | 28.9 | 1.4 | 19.6 | 50.1 | 0 | 0 | 1002 | -0.53 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:48 | 28.4 | 1.6 | 19.4 | 50.6 | 0 | 0 | 1002 | 0.26 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:53 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1002 | -0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:05 | 0 | 2.5 | 19.5 | 78 | 0 | 0 | 1002 | 0.14 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:09 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | -0.77 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:13 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 1002 | 0.56 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:16 | 0 | 1.5 | 19.4 | 79.1 | 0 | 0 | 1002 | 0.34 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:19 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 1002 | -0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:22 | 0 | 2.4 | 18.9 | 78.7 | 0 | 0 | 1002 | 0.26 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:29 | 0.3 | 2.8 | 19.2 | 77.7 | 0 | 0 | 1002 | 0.31 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:55 | 0.5 | 2.1 | 19.6 | 77.8 | 0 | 0 | 1002 | 0.87 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:59 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1002 | 0.9 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:02 | 0.1 | 2.5 | 20 | 77.4 | 0 | 0 | 1002 | -0.75 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:07 | 0.2 | 1.4 | 20 | 78.4 | 0 | 0 | 1002 | -0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:12 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 1002 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:15 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | 0.68 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:19 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 1002 | -0.71 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2016-11-16
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 12 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:15 | 49.6 | 38.8 | 0.6 | 11 | 12 | 8 | 1000 | 160 |  | Flare On 400 KWH
GV1 |  | 33.6 | 25.6 | 1.4 | 39.4 | 10 | 5 | 1000 | -0.89 |  | OFF
GV3 |  | 50.1 | 36.5 | 0.3 | 13.1 | 9 | 4 | 1000 | -28.98 |  | Open Full
GV4 |  | 46.5 | 34.9 | 1 | 17.6 | 6 | 7 | 1000 | -5.69 |  | Cracked Open
GV6 |  | 46.9 | 36.4 | 1.1 | 15.6 | 9 | 4 | 1000 | -5.99 |  | Cracked Open
GV7 |  | 31.9 | 28.7 | 2.6 | 36.8 | 6 | 6 | 1000 | -0.77 |  | Off Low Gas high o2
GV8 |  | 32.7 | 33.6 | 2.4 | 31.3 | 8 | 3 | 1000 | -0.51 |  | Off Low Gas high o3
GV9 |  | 48.5 | 37 | 0.4 | 14.1 | 7 | 8 | 1000 | -28.74 |  | Open Full
GV10 |  | 41.9 | 35.9 | 1.3 | 20.9 | 4 | 14 | 1000 | -1.25 |  | Off
GV11 |  | 45 | 33 | 1.2 | 20.8 | 5 | 4 | 1000 | -5.99 |  | Cracked Open
GV12+R3 Manifold |  | 50 | 36.5 | 0.5 | 13 | 11 | 11 | 1000 | -28.71 |  | Open Full
GV12 |  | 50.4 | 36.8 | 0.4 | 12.4 | 13 | 12 | 1000 | -28.55 |  | Open Full
R3 |  | 49.4 | 35.4 | 0.7 | 14.5 | 9 | 10 | 1000 | -29.01 |  | Open Full
GV13 |  | 1.6 | 2.6 | 20 | 75.8 | 7 | 5 | 1000 | -0.78 |  | Left Closed
GV14 |  | 49.8 | 37.1 | 0.6 | 12.5 | 10 | 6 | 1000 | -29.21 |  | Open Full
GV15 |  | 49 | 36 | 0.4 | 14.6 | 7 | 10 | 1000 | -28.41 |  | Open Full
GV16 |  | 45.6 | 36.5 | 1.1 | 16.8 | 8 | 10 | 1000 | -5.63 |  | Left Cracked
GV17+LC4 Manifold |  | 45.8 | 35.6 | 2.4 | 16.2 | 8 | 9 | 1000 | -0.21 |  | Off at Manifold Gas drops quick.
GV17 |  | 44 | 35 | 2 | 19 | 9 | 7 | 1000 | -0.24 |  | Open Full at Well
LC4 |  | 46.6 | 35.9 | 2.7 | 14.8 | 6 | 11 | 1000 | -0.14 |  | Open Full at well
GV18 |  | 49.2 | 37 | 0.4 | 13.4 | 2 | 7 | 1000 | -28.25 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 43 | 37.4 | 2.1 | 17.5 | 9 | 2 | 1000 | -1.42 |  | Off gas drops off quick.
GV23 |  | 49.8 | 37 | 0.3 | 12.9 | 10 | 9 | 1000 | -28.47 |  | Open Full
GV24 |  | 50.2 | 36.9 | 0.6 | 12.3 | 7 | 5 | 1000 | -28.63 |  | Open Full
GV25 |  | 42 | 37.9 | 1.4 | 18.7 | 11 | 6 | 1000 | -0.87 |  | Left Closed
GV26 + 27 Manifold |  | 50.5 | 37 | 0.4 | 12.1 | 9 | 3 | 1000 | -28.47 |  | Open Full
GV28+ 29 Manifold |  | 50.4 | 37.2 | 0.3 | 12.1 | 8 | 8 | 1000 | -28.36 |  | Open Full
GV26 |  | 50.4 | 36.4 | 0.2 | 13 | 12 | 6 | 1000 | -28.77 |  | Open Full
GV27 |  | 51.2 | 37.5 | 0.5 | 10.8 | 11 | 2 | 1000 | -28.23 |  | Open Full
GV28 |  | 50.9 | 36.4 | 0.1 | 12.6 | 7 | 8 | 1000 | -28.21 |  | Open Full
GV29 |  | 50.2 | 37 | 0.3 | 12.5 | 9 | 6 | 1000 | -28.54 |  | Open Full
GVA |  | 33.9 | 26.7 | 5 | 34.4 | 8 | 7 | 1000 | -1 |  | Off Low gas
B+C Manifold |  | 49.6 | 35.9 | 0.4 | 14.1 | 9 | 7 | 1000 | -28.56 |  | Open Full
GV B |  | 50 | 34.9 | 0.3 | 14.8 | 11 | 9 | 1000 | -28.45 |  | Open Full
GV C |  | 49 | 37 | 0.5 | 13.5 | 6 | 3 | 1000 | -28.69 |  | Open Full
GV30 |  | 47.2 | 35.9 | 1.2 | 15.7 | 3 | 7 | 1000 | -6 |  | Left Cracked
GV31 |  | 44.9 | 36.2 | 1 | 17.9 | 12 | 15 | 1000 | -5.87 |  | Cracked Open
GV32 |  | 45.2 | 35.6 | 1.2 | 18 | 14 | 9 | 1000 | -5.29 |  | Cracked Open
GV33 |  | 44.8 | 37 | 1.1 | 17.1 | 8 | 3 | 1000 | -5.89 |  | Cracked Open
GV34 |  | 45.3 | 36.9 | 1.1 | 16.7 | 9 | 8 | 1000 | -6.02 |  | Cracked Open
GV 35 (New Well) |  | 20.1 | 23.9 | 1.7 | 54.3 | 10 | 7 | 1000 | -1.02 |  | Left Closed
GV 36 (New Well) |  | 22.9 | 21.9 | 4.5 | 50.7 | 8 | 4 | 1000 | -1.24 |  | OFF low gas.
GV 37 (New Well) |  | 49.8 | 37.4 | 0.3 | 12.5 | 7 | 8 | 1000 | -28.36 |  | Left open Full
GV 38 (New Well) |  | 46.9 | 35.9 | 1.1 | 16.1 | 9 | 6 | 1000 | -6 |  | Cracked Open
GV 39 (New Well) |  | 46 | 36.5 | 1.4 | 16.1 | 12 | 5 | 1000 | -5.87 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 45.8 | 36.9 | 1.1 | 16.2 | 14 | 3 | 1000 | -6.23 |  | Cracked Open
GV 41 (New Well) |  | 45.3 | 35.9 | 1.3 | 17.5 | 4 | 9 | 1000 | -7 |  | Cracked Open
GV 42 (New Well) |  | 39.9 | 36.5 | 1.2 | 22.4 | 9 | 7 | 1000 | -1.14 |  | Off Low Gas
GV 43 (New Well) |  | 47 | 36.5 | 1.2 | 15.3 | 7 | 7 | 1000 | -5.57 |  | Cracked open
GV 44 (New Well) |  | 39.7 | 36 | 1.3 | 23 | 8 | 11 | 1000 | -0.87 |  | Off Low gas
GV 45 (New Well) |  | 47.1 | 37.4 | 1 | 14.5 | 14 | 12 | 1000 | -5.88 |  | Cracked Open
GV 46 (New Well) |  | 47.5 | 38 | 0.3 | 14.2 | 9 | 6 | 1000 | -28.47 |  | Open Full
GV 47 (New Well) |  | 46 | 36 | 1 | 17 | 10 | 11 | 1000 | -6.32 |  | Cracked Opem
GV 48 (New Well) |  | 59.8 | 40 | 0 | 0.2 | 9 | 5 | 1000 | -28.16 |  | Open Full
GV 49 (New Well) |  | 45.9 | 35.2 | 1 | 17.9 | 10 | 6 | 1000 | -5.87 |  | Cracked open
LC1B |  | 36.9 | 36 | 2 | 25.1 | 8 | 8 | 1000 | -1.04 |  | OFF
LC2R? |  | 50.1 | 37.9 | 0.3 | 11.7 | 7 | 7 | 1000 | -28.89 |  | Open Full
GV 2.1 |  | 49.6 | 38 | 0.4 | 12 | 5 | 4 | 1000 | -27.99 |  | Open Full
GV 2.2+ LC2B MAN |  | 48.5 | 36.2 | 1.1 | 14.2 | 11 | 12 | 1000 | -7.52 |  | Cracked Open at Manifold
GV 2.2 |  | 47.8 | 36.3 | 1 | 14.9 | 10 | 10 | 1000 | -7.89 |  | Cracked Open
LC2B |  | 49 | 35.8 | 1.3 | 13.9 | 13 | 14 | 1000 | -7.24 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 48 | 37.2 | 0.8 | 14 | 10 | 9 | 1000 | -14.01 |  | Left Open Half Way
LC3.1 |  | 48 | 37.2 | 0.8 | 14 | 12 | 5 | 1000 | -14.01 |  | Left open half way
LC3 |  | 46.2 | 34.5 | 2.3 | 17 | 6 | 7 | 1000 | -0.89 |  | OFF
LC4B |  | 48.2 | 36.5 | 1.1 | 14.2 | 14 | 8 | 1000 | -6.57 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.5 | 36.5 | 0.7 | 14.3 | 8 | 9 | 1000 | -28.45 |  | Open Full
R1 |  | 47.6 | 35.6 | 1.2 | 15.6 | 8 | 9 | 1000 | -7.48 |  | Cracked Open
R1B |  | 49 | 37 | 0.5 | 13.5 | 9 | 7 | 1000 | -29 |  | Open Full
R2B |  | 48.7 | 37.8 | 0.7 | 12.8 | 7 | 5 | 1000 | -26.58 |  | Open Full
R4B |  | 41.8 | 36.2 | 3.6 | 18.4 | 6 | 8 | 1000 | -0.54 |  | Left closed
R6B |  | 50.9 | 38 | 0.6 | 10.5 | 9 | 4 | 1000 | -28.69 |  | Open Full
LC5 |  | 46.5 | 35.9 | 3.3 | 14.3 | 8 | 7 | 1000 | -0.21 |  | Left Off ( Gas drops quick)
LC6 |  | 46.9 | 34.9 | 2.4 | 15.8 | 10 | 4 | 1000 | -0.36 |  | Left Off ( Gas drops quick)
LC6B |  | 51 | 35.9 | 0.9 | 12.2 | 7 | 7 | 1000 | -28.74 |  | Open Full
PW1 |  | 1.5 | 0.4 | 13.5 | 84.6 | 11 | 4 | 1000 | -0.89 |  | Left Off
PW2 |  | 34.5 | 19 | 3.4 | 43.1 | 14 | 2 | 1000 | 0.23 |  | Left Off
PW3 |  | 32.9 | 19.8 | 2.5 | 44.8 | 6 | 6 | 1000 | 0.14 |  | Left Off
PW4 |  | 46.2 | 35.9 | 1.2 | 16.7 | 6 | 6 | 1000 | -5.24 |  | Cracked Open
PW5 |  | 33.6 | 26.4 | 1.7 | 38.3 | 12 | 8 | 1000 | -0.89 |  | Left Off
PW6 |  | 34.1 | 25.7 | 2.4 | 37.8 | 10 | 8 | 1000 | -0.88 |  | Left Off
Flare | 15:50 | 49.9 | 38.6 | 0.6 | 10.9 | 11 | 8 | 1000 | 160 |  | Engine Off (Awaiting new engine) Flaring Running 400 KW/H
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.

## December
Date | 2016-12-01
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 4 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:00 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1001 | 0.39 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:05 | 0.2 | 1.1 | 19.6 | 79.1 | 0 | 0 | 1001 | -0.55 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:07 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1001 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:09 | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 1001 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:13 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 1001 | 0.59 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:16 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1001 | 0.31 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:19 | 28.9 | 1.3 | 20 | 49.8 | 0 | 0 | 1001 | -0.37 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:25 | 28.4 | 1.4 | 19.6 | 50.6 | 0 | 0 | 1001 | 0.61 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:30 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1001 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:42 | 0 | 2 | 19.3 | 78.7 | 0 | 0 | 1001 | -0.11 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:46 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1001 | 0.4 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:50 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 1001 | -0.8 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:53 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1001 | 0.43 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:56 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1001 | 0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:59 | 0 | 2 | 19.2 | 78.8 | 0 | 0 | 1001 | 0.61 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:06 | 0.3 | 2.1 | 19.4 | 78.2 | 0 | 0 | 1001 | 0.57 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:33 | 0.5 | 1.8 | 19.9 | 77.8 | 0 | 0 | 1001 | -0.35 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:36 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1001 | 0.31 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:39 | 0.3 | 2.2 | 19.9 | 77.6 | 0 | 0 | 1001 | 0.15 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:44 | 0.2 | 1.1 | 20.1 | 78.6 | 0 | 0 | 1001 | 0.26 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:49 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1001 | 0.59 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:52 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1001 | -0.62 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:56 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 1001 | 0.58 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-12-08
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 1 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:30 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1004 | 0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:35 | 0.3 | 1.4 | 19.8 | 78.5 | 0 | 0 | 1004 | -0.63 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:37 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1004 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:39 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1004 | 0.35 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:43 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 1004 | 0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:46 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1004 | 0.44 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:49 | 29 | 1.5 | 19.8 | 49.7 | 0 | 0 | 1004 | -0.37 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:55 | 28.6 | 1.6 | 19.7 | 50.1 | 0 | 0 | 1004 | 0.68 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:00 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1004 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:12 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1004 | -0.23 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:16 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 1004 | 0.39 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:20 | 0 | 2 | 20 | 78 | 0 | 0 | 1004 | -0.74 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:23 | 0 | 1.6 | 19.1 | 79.3 | 0 | 0 | 1004 | 0.48 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:26 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1004 | 0.26 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:29 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 1004 | 0.7 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:36 | 0.2 | 2 | 19.6 | 78.2 | 0 | 0 | 1004 | 0.49 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:03 | 0.4 | 1.5 | 20 | 78.1 | 0 | 0 | 1004 | -0.23 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:06 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1004 | 0.37 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:09 | 0.2 | 2 | 20.1 | 77.7 | 0 | 0 | 1004 | 0.21 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:14 | 0.3 | 1.2 | 19.7 | 78.8 | 0 | 0 | 1004 | 0.2 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:19 | 0 | 2.6 | 19.5 | 77.9 | 0 | 0 | 1004 | 0.67 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:22 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1004 | -0.55 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:26 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1004 | 0.67 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2016-12-15
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 2 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:27 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:32 | 0.4 | 1.5 | 20 | 78.1 | 0 | 0 | 1002 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:34 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1002 | 0.41 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:36 | 0 | 0.4 | 19.6 | 80 | 0 | 0 | 1002 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:39 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.71 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:43 | 0 | 2 | 20.1 | 77.9 | 0 | 0 | 1002 | 0.92 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:46 | 29.2 | 1.4 | 20 | 49.4 | 0 | 0 | 1002 | 0.84 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:52 | 28.2 | 2.3 | 19.4 | 50.1 | 0 | 0 | 1002 | 0.86 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:57 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1002 | 0.91 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:09 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 1002 | -0.75 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:13 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 1002 | 0.71 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:17 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1002 | -0.74 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:20 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 1002 | 0.52 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:23 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1002 | 0.74 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:26 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | 1.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:33 | 0.3 | 2.1 | 20.1 | 77.5 | 0 | 0 | 1002 | 0.95 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:59 | 0.2 | 1.9 | 19.8 | 78.1 | 0 | 0 | 1002 | 0.54 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:03 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | 0.87 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:06 | 0.3 | 1.8 | 20 | 77.9 | 0 | 0 | 1002 | 0.77 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:11 | 0.1 | 1.2 | 19.5 | 79.2 | 0 | 0 | 1002 | 0.79 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:16 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 1002 | 0.79 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:19 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | -0.46 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:23 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.87 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-12-22
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 1 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 996 | 0.89 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.3 | 1.4 | 20.1 | 78.2 | 0 | 0 | 996 | -0.64 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:28 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 996 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:31 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 996 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 996 | 0.68 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 996 | 0.89 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 29 | 1.5 | 19.8 | 49.7 | 0 | 0 | 996 | 0.78 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:47 | 28.4 | 2.4 | 19.6 | 49.6 | 0 | 0 | 996 | 0.88 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 1 | 19.2 | 79.8 | 0 | 0 | 996 | 0.98 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 996 | -0.85 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 1.9 | 19.3 | 78.8 | 0 | 0 | 996 | 0.58 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:02 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 996 | -0.88 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 996 | 0.62 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 2.3 | 19.7 | 78 | 0 | 0 | 996 | 0.84 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 3 | 19.6 | 77.4 | 0 | 0 | 996 | 1.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.4 | 2 | 19.9 | 77.7 | 0 | 0 | 996 | 0.91 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.2 | 1.6 | 19.9 | 78.3 | 0 | 0 | 996 | 0.63 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 2 | 20 | 78 | 0 | 0 | 996 | 0.9 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.2 | 1.6 | 19.8 | 78.4 | 0 | 0 | 996 | 0.87 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.2 | 1.4 | 19.6 | 78.8 | 0 | 0 | 996 | 0.72 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 2.8 | 19.7 | 77.5 | 0 | 0 | 996 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 996 | -0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 2.4 | 20.1 | 77.5 | 0 | 0 | 996 | 0.93 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2016-12-27
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 1 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:19 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | -0.35 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:24 | 0.2 | 1.6 | 20 | 78.2 | 0 | 0 | 999 | 0.76 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:25 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 999 | 0.45 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:27 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:31 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 999 | 0.52 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:35 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 999 | 0.48 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:38 | 29.2 | 1.4 | 20 | 49.4 | 0 | 0 | 999 | -0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:44 | 28 | 2.3 | 19.9 | 49.8 | 0 | 0 | 999 | 0.36 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:49 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 999 | -0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:01 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 999 | 0.16 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:05 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | 0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:09 | 0 | 2.2 | 20.1 | 77.7 | 0 | 0 | 999 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:12 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 999 | 0.35 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:15 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 999 | -0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:18 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 999 | 0.48 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:25 | 0.3 | 2.3 | 19.5 | 77.9 | 0 | 0 | 999 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:51 | 0.1 | 1.4 | 19.6 | 78.9 | 0 | 0 | 999 | 0.25 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:55 | 0 | 2.3 | 19.4 | 78.3 | 0 | 0 | 999 | 0.69 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:58 | 0.3 | 1.9 | 19.3 | 78.5 | 0 | 0 | 999 | -0.17 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:03 | 0.4 | 1.1 | 19.7 | 78.8 | 0 | 0 | 999 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:08 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 999 | 0.39 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:11 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:15 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 999 | 0.28 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date |  | 2016-12-14
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 6 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:15 | 49.2 | 37.8 | 0.5 | 12.5 | 11 | 9 | 1004 | 165 |  | Flare On 400 KWH
GV1 |  | 34.5 | 26.9 | 1.3 | 37.3 | 8 | 6 | 1004 | -0.56 |  | OFF
GV3 |  | 50 | 36.9 | 0.4 | 12.7 | 6 | 5 | 1004 | -25.89 |  | Open Full
GV4 |  | 46.8 | 35.2 | 1 | 17 | 4 | 2 | 1004 | -6.23 |  | Cracked Open
GV6 |  | 46.5 | 37 | 1.1 | 15.4 | 12 | 3 | 1004 | -6.47 |  | Cracked Open
GV7 |  | 30.5 | 29.8 | 2.5 | 37.2 | 11 | 3 | 1004 | -0.55 |  | Off Low Gas high o2
GV8 |  | 31.7 | 32.9 | 2.2 | 33.2 | 9 | 6 | 1004 | -0.47 |  | Off Low Gas high o3
GV9 |  | 48.9 | 36.9 | 0.3 | 13.9 | 8 | 8 | 1004 | -25.74 |  | Open Full
GV10 |  | 42.3 | 35.2 | 1.2 | 21.3 | 9 | 9 | 1004 | -1 |  | Off
GV11 |  | 44.5 | 34.5 | 1.1 | 19.9 | 6 | 11 | 1004 | -6.45 |  | Cracked Open
GV12+R3 Manifold |  | 49.8 | 35.6 | 0.4 | 14.2 | 11 | 6 | 1004 | -25.78 |  | Open Full
GV12 |  | 50.1 | 36.5 | 0.3 | 13.1 | 12 | 3 | 1004 | -25.51 |  | Open Full
R3 |  | 49 | 35.8 | 0.6 | 14.6 | 11 | 7 | 1004 | -25.91 |  | Open Full
GV13 |  | 1.9 | 2.9 | 19.8 | 75.4 | 9 | 3 | 1004 | -0.65 |  | Left Closed
GV14 |  | 49.2 | 36.7 | 0.5 | 13.6 | 5 | 6 | 1004 | -25.45 |  | Open Full
GV15 |  | 49.5 | 36.5 | 0.4 | 13.6 | 7 | 5 | 1004 | -25.99 |  | Open Full
GV16 |  | 46.9 | 36.2 | 1 | 15.9 | 4 | 6 | 1004 | -6.02 |  | Left Cracked
GV17+LC4 Manifold |  | 46.3 | 36 | 2.3 | 15.4 | 8 | 11 | 1004 | -0.29 |  | Off at Manifold Gas drops quick.
GV17 |  | 45 | 36.3 | 2 | 16.7 | 11 | 11 | 1004 | -0.25 |  | Open Full at Well
LC4 |  | 46.9 | 36 | 2.6 | 14.5 | 5 | 10 | 1004 | -0.32 |  | Open Full at well
GV18 |  | 49.2 | 37 | 0.4 | 13.4 | 3 | 8 | 1004 | -25.74 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 44.5 | 37.4 | 1.9 | 16.2 | 9 | 3 | 1004 | -1.24 |  | Off gas drops off quick.
GV23 |  | 49.5 | 35.9 | 0.4 | 14.2 | 11 | 8 | 1004 | -25.54 |  | Open Full
GV24 |  | 49.6 | 36 | 0.5 | 13.9 | 8 | 6 | 1004 | -25.59 |  | Open Full
GV25 |  | 43.9 | 35.9 | 1.2 | 19 | 7 | 11 | 1004 | -0.74 |  | Left Closed
GV26 + 27 Manifold |  | 50.1 | 37.5 | 0.5 | 11.9 | 10 | 5 | 1004 | -25.99 |  | Open Full
GV28+ 29 Manifold |  | 49.9 | 37.5 | 0.4 | 12.2 | 9 | 8 | 1004 | -26.01 |  | Open Full
GV26 |  | 50.4 | 36.4 | 0.2 | 13 | 11 | 9 | 1004 | -25.47 |  | Open Full
GV27 |  | 49.9 | 37.5 | 0.5 | 12.1 | 9 | 6 | 1004 | -26.23 |  | Open Full
GV28 |  | 50.2 | 36.4 | 0.1 | 13.3 | 8 | 9 | 1004 | -26.45 |  | Open Full
GV29 |  | 49.5 | 37 | 0.3 | 13.2 | 9 | 8 | 1004 | -25.87 |  | Open Full
GVA |  | 34.5 | 27.9 | 4.9 | 32.7 | 8 | 5 | 1004 | -0.87 |  | Off Low gas
B+C Manifold |  | 50.2 | 36.9 | 0.5 | 12.4 | 7 | 4 | 1004 | -25.77 |  | Open Full
GV B |  | 50.5 | 35.6 | 0.4 | 13.5 | 10 | 7 | 1004 | -25.69 |  | Open Full
GV C |  | 49.8 | 37.5 | 0.6 | 12.1 | 6 | 2 | 1004 | -25.98 |  | Open Full
GV30 |  | 47 | 36 | 1 | 16 | 8 | 11 | 1004 | -6.89 |  | Left Cracked
GV31 |  | 44.5 | 36 | 1.1 | 18.4 | 10 | 16 | 1004 | -6.23 |  | Cracked Open
GV32 |  | 45.9 | 35.9 | 1 | 17.2 | 12 | 12 | 1004 | -6.47 |  | Cracked Open
GV33 |  | 45.3 | 36.4 | 1 | 17.3 | 11 | 14 | 1004 | -6.21 |  | Cracked Open
GV34 |  | 45.9 | 36.5 | 1 | 16.6 | 10 | 8 | 1004 | -6.23 |  | Cracked Open
GV 35 (New Well) |  | 20.9 | 24.9 | 1.5 | 52.7 | 8 | 9 | 1004 | -1.23 |  | Left Closed
GV 36 (New Well) |  | 23.9 | 22.3 | 4.2 | 49.6 | 6 | 3 | 1004 | -1.45 |  | OFF low gas.
GV 37 (New Well) |  | 49.9 | 36.9 | 0.2 | 13 | 3 | 11 | 1004 | -25.47 |  | Left open Full
GV 38 (New Well) |  | 46 | 35.5 | 1 | 17.5 | 10 | 10 | 1004 | -7 |  | Cracked Open
GV 39 (New Well) |  | 46.2 | 35.9 | 1.3 | 16.6 | 9 | 3 | 1004 | -6.56 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 45.2 | 36.4 | 1 | 17.4 | 8 | 9 | 1004 | -6.89 |  | Cracked Open
GV 41 (New Well) |  | 45.9 | 36 | 1 | 17.1 | 8 | 7 | 1004 | -6.78 |  | Cracked Open
GV 42 (New Well) |  | 40 | 35.9 | 1.1 | 23 | 10 | 8 | 1004 | -1.23 |  | Off Low Gas
GV 43 (New Well) |  | 46.8 | 36 | 1.2 | 16 | 11 | 16 | 1004 | -6.24 |  | Cracked open
GV 44 (New Well) |  | 39.5 | 36.2 | 1.4 | 22.9 | 14 | 12 | 1004 | -0.74 |  | Off Low gas
GV 45 (New Well) |  | 47.2 | 37 | 1.1 | 14.7 | 17 | 17 | 1004 | -6.21 |  | Cracked Open
GV 46 (New Well) |  | 48 | 36.5 | 0.4 | 15.1 | 11 | 11 | 1004 | -25.3 |  | Open Full
GV 47 (New Well) |  | 46.2 | 36.2 | 1.1 | 16.5 | 9 | 12 | 1004 | -7.21 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 8 | 4 | 1004 | -25.47 |  | Open Full
GV 49 (New Well) |  | 46.2 | 35.4 | 1.1 | 17.3 | 6 | 9 | 1004 | -6.3 |  | Cracked open
LC1B |  | 37 | 36.8 | 1.9 | 24.3 | 11 | 8 | 1004 | -1.08 |  | OFF
LC2R? |  | 50.2 | 36.8 | 0.4 | 12.6 | 7 | 9 | 1004 | -25.49 |  | Open Full
GV 2.1 |  | 49.2 | 37.8 | 0.3 | 12.7 | 6 | 11 | 1004 | -25.69 |  | Open Full
GV 2.2+ LC2B MAN |  | 48 | 36.5 | 1.2 | 14.3 | 8 | 11 | 1004 | -7.99 |  | Cracked Open at Manifold
GV 2.2 |  | 47.5 | 36.9 | 1.1 | 14.5 | 10 | 9 | 1004 | -8.06 |  | Cracked Open
LC2B |  | 48.6 | 36 | 1.3 | 14.1 | 8 | 13 | 1004 | -7.87 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 48.6 | 37.2 | 0.9 | 13.3 | 4 | 9 | 1004 | -14.56 |  | Left Open Half Way
LC3.1 |  | 48.6 | 37.2 | 0.9 | 13.3 | 6 | 7 | 1004 | -14.56 |  | Left open half way
LC3 |  | 46 | 33.9 | 2 | 18.1 | 3 | 10 | 1004 | -0.54 |  | OFF
LC4B |  | 48.6 | 36 | 1.2 | 14.2 | 3 | 8 | 1004 | -7.45 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.2 | 36.9 | 0.8 | 14.1 | 6 | 9 | 1004 | -25.45 |  | Open Full
R1 |  | 47.5 | 36.2 | 1 | 15.3 | 4 | 10 | 1004 | -8.06 |  | Cracked Open
R1B |  | 49.1 | 37.4 | 0.6 | 12.9 | 8 | 7 | 1004 | -25.56 |  | Open Full
R2B |  | 49 | 38 | 0.8 | 12.2 | 3 | 5 | 1004 | -25.47 |  | Open Full
R4B |  | 42.6 | 36.9 | 3.5 | 17 | 2 | 6 | 1004 | -0.45 |  | Left closed
R6B |  | 51 | 38.6 | 0.2 | 10.2 | 14 | 4 | 1004 | -25.71 |  | Open Full
LC5 |  | 47 | 34.9 | 3 | 15.1 | 4 | 11 | 1004 | -0.29 |  | Left Off ( Gas drops quick)
LC6 |  | 45.9 | 35.9 | 2.6 | 15.6 | 1 | 2 | 1004 | -0.95 |  | Left Off ( Gas drops quick)
LC6B |  | 51.2 | 36.5 | 0.8 | 11.5 | 7 | 9 | 1004 | -25.44 |  | Open Full
PW1 |  | 1.9 | 0.5 | 12.9 | 84.7 | 11 | 6 | 1004 | -0.56 |  | Left Off
PW2 |  | 33.6 | 19.8 | 2.6 | 44 | 5 | 8 | 1004 | 0.29 |  | Left Off
PW3 |  | 33.2 | 19.9 | 2.1 | 44.8 | 6 | 9 | 1004 | 0.17 |  | Left Off
PW4 |  | 46.5 | 36 | 1.3 | 16.2 | 8 | 6 | 1004 | -6.23 |  | Cracked Open
PW5 |  | 34.5 | 26.9 | 1.5 | 37.1 | 9 | 1 | 1004 | -0.75 |  | Left Off
PW6 |  | 34.5 | 26.8 | 2.9 | 35.8 | 8 | 4 | 1004 | -0.56 |  | Left Off
Flare | 15:50 | 49.2 | 37.9 | 0.5 | 12.4 | 11 | 8 | 1004 | 165 |  | Engine Off (Awaiting new engine) Flaring Running 400 KW/H
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## January 2017
Date | 2017-01-05
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 3 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:36 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1002 | -0.63 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:41 | 0.1 | 1.3 | 19.8 | 78.8 | 0 | 0 | 1002 | -0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:43 | 0 | 1.1 | 19 | 79.9 | 0 | 0 | 1002 | -0.35 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:45 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1002 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:48 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1002 | -0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:52 | 0 | 2.3 | 19.1 | 78.6 | 0 | 0 | 1002 | 0.35 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:55 | 29 | 1.9 | 20 | 49.1 | 0 | 0 | 1002 | -0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:01 | 28.2 | 2.1 | 19.9 | 49.8 | 0 | 0 | 1002 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:06 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1002 | 0.38 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:18 | 0 | 2.5 | 19.7 | 77.8 | 0 | 0 | 1002 | -0.96 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:22 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 1002 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:26 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 1002 | 0.24 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:29 | 0 | 1.4 | 19.2 | 79.4 | 0 | 0 | 1002 | -0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:32 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1002 | 0.38 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:35 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1002 | -0.77 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:42 | 0.4 | 2.6 | 19.2 | 77.8 | 0 | 0 | 1002 | -0.65 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:08 | 0.2 | 1.9 | 19.7 | 78.2 | 0 | 0 | 1002 | -78 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:12 | 0 | 2.5 | 19.6 | 77.9 | 0 | 0 | 1002 | 0.63 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:15 | 0.2 | 1.8 | 19.8 | 78.2 | 0 | 0 | 1002 | -0.87 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:20 | 0.2 | 2 | 19.9 | 77.9 | 0 | 0 | 1002 | -0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:25 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | -0.48 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:28 | 0 | 0.4 | 19.9 | 79.7 | 0 | 0 | 1002 | -0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:32 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.86 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-01-12
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 3 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:45 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1002 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:50 | 0.2 | 1.2 | 20 | 78.6 | 0 | 0 | 1002 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:51 | 0 | 1 | 19.5 | 79.5 | 0 | 0 | 1002 | 0.42 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:53 | 0 | 0.9 | 19.6 | 79.5 | 0 | 0 | 1002 | -0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:57 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 1002 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:01 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:04 | 28.5 | 1.5 | 19.9 | 50.1 | 0 | 0 | 1002 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:10 | 28 | 2.4 | 20 | 49.6 | 0 | 0 | 1002 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:15 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1002 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:27 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:31 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1002 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:35 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1002 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:38 | 0 | 1.8 | 19.7 | 78.5 | 0 | 0 | 1002 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:41 | 0 | 2.6 | 19.4 | 78 | 0 | 0 | 1002 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:44 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1002 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:51 | 0.3 | 2.8 | 19.8 | 77.1 | 0 | 0 | 1002 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:17 | 0.3 | 1.5 | 20 | 78.2 | 0 | 0 | 1002 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:21 | 0 | 2.8 | 19.6 | 77.6 | 0 | 0 | 1002 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:24 | 0.4 | 1.5 | 19.8 | 78.3 | 0 | 0 | 1002 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:29 | 0.3 | 2.1 | 19.6 | 78 | 0 | 0 | 1002 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:34 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 1002 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:37 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1002 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:41 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-01-19
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 4 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:23 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 998 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:28 | 0.4 | 1.4 | 19.9 | 78.3 | 0 | 0 | 998 | 0.38 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:29 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 998 | 0.48 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 998 | -0.58 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:35 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 998 | 0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:39 | 0 | 2.5 | 19.6 | 77.9 | 0 | 0 | 998 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:42 | 28.5 | 1.8 | 19.8 | 49.9 | 0 | 0 | 998 | 0.58 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:48 | 28.5 | 2.6 | 19.7 | 49.2 | 0 | 0 | 998 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:53 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 998 | 0.68 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:05 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 998 | 0.87 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:09 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 998 | 0.59 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:13 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 998 | 0.23 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:16 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 998 | 0.87 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:19 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 998 | -0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:22 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 998 | 0.23 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:29 | 0.4 | 2.5 | 20 | 77.1 | 0 | 0 | 998 | -0.46 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:55 | 0.1 | 1.7 | 19.7 | 78.5 | 0 | 0 | 998 | 0.68 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:59 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 998 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:02 | 0.2 | 1.5 | 19.5 | 78.8 | 0 | 0 | 998 | -0.15 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:07 | 0.2 | 3 | 19.9 | 76.9 | 0 | 0 | 998 | 0.24 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:12 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 998 | 0.25 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:15 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 998 | -0.78 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:19 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 998 | 0.52 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-01-26
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 4 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1002 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.3 | 1.1 | 19.8 | 78.8 | 0 | 0 | 1002 | -0.12 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1002 | -0.19 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 1002 | 0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1002 | 0.77 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2.3 | 19.4 | 78.3 | 0 | 0 | 1002 | 0.52 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 28.4 | 1.6 | 19.9 | 50.1 | 0 | 0 | 1002 | 0.46 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.8 | 2.4 | 20 | 48.8 | 0 | 0 | 1002 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1002 | 0.36 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 2.7 | 19.8 | 77.5 | 0 | 0 | 1002 | -0.25 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1002 | -0.11 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1002 | 0.69 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | 0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 3 | 20 | 77 | 0 | 0 | 1002 | -0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | 0.29 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 2.1 | 19.3 | 78.3 | 0 | 0 | 1002 | -0.26 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.2 | 1.8 | 19.7 | 78.3 | 0 | 0 | 1002 | 0.52 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 1002 | 0.46 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.1 | 1.4 | 20 | 78.5 | 0 | 0 | 1002 | -0.68 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.4 | 3.2 | 19.8 | 76.6 | 0 | 0 | 1002 | -0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 3.2 | 19.4 | 77.4 | 0 | 0 | 1002 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1002 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.7 | 19.9 | 77.4 | 0 | 0 | 1002 | 0.38 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date |  | 2017-01-11
Weather: |  | Dry
Wind conditions: |  | Calm
Air Temperature: |  | 5 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:00 | 51.2 | 38.4 | 0.4 | 10 | 7 | 7 | 999 | 170 |  | Flare On 400 KWH
GV1 |  | 33.9 | 27.4 | 1 | 37.7 | 8 | 8 | 999 | -0.35 |  | OFF
GV3 |  | 51.2 | 37.9 | 0.3 | 10.6 | 7 | 11 | 999 | -24.57 |  | Open Full
GV4 |  | 45.1 | 36.2 | 1.1 | 17.6 | 8 | 2 | 999 | -6.02 |  | Cracked Open
GV6 |  | 44.9 | 37.2 | 1.2 | 16.7 | 8 | 5 | 999 | -6.23 |  | Cracked Open
GV7 |  | 31.6 | 30 | 2.4 | 36 | 6 | 9 | 999 | -0.59 |  | Off Low Gas high o2
GV8 |  | 29.9 | 33.8 | 2.8 | 33.5 | 5 | 5 | 999 | -0.47 |  | Off Low Gas high o3
GV9 |  | 49.6 | 37 | 0.2 | 13.2 | 11 | 4 | 999 | -24.59 |  | Open Full
GV10 |  | 39.9 | 36 | 1.6 | 22.5 | 7 | 6 | 999 | -0.89 |  | Off
GV11 |  | 46 | 33.9 | 1.2 | 18.9 | 7 | 8 | 999 | -6.22 |  | Cracked Open
GV12+R3 Manifold |  | 50 | 36.9 | 0.5 | 12.6 | 4 | 6 | 999 | -24.36 |  | Open Full
GV12 |  | 50.4 | 36.4 | 0.7 | 12.5 | 2 | 8 | 999 | -24.11 |  | Open Full
R3 |  | 49.5 | 35 | 0.3 | 15.2 | 5 | 4 | 999 | -24.58 |  | Open Full
GV13 |  | 1.8 | 3.2 | 19.5 | 75.5 | 8 | 7 | 999 | -0.32 |  | Left Closed
GV14 |  | 49 | 36 | 0.3 | 14.7 | 8 | 4 | 999 | -24 |  | Open Full
GV15 |  | 49.8 | 36.9 | 0.4 | 12.9 | 7 | 6 | 999 | -24.87 |  | Open Full
GV16 |  | 46 | 35.2 | 1.2 | 17.6 | 6 | 8 | 999 | -6 |  | Left Cracked
GV17+LC4 Manifold |  | 46.5 | 36.5 | 2.4 | 14.6 | 13 | 9 | 999 | -0.36 |  | Off at Manifold Gas drops quick.
GV17 |  | 45.2 | 36.8 | 2.1 | 15.9 | 14 | 10 | 999 | -0.29 |  | Open Full at Well
LC4 |  | 47 | 36.1 | 2.6 | 14.3 | 12 | 8 | 999 | -0.4 |  | Open Full at well
GV18 |  | 49.8 | 37.4 | 0.2 | 12.6 | 11 | 7 | 999 | -24.23 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 45 | 37.8 | 1.8 | 15.4 | 11 | 5 | 999 | -1.08 |  | Off gas drops off quick.
GV23 |  | 49.5 | 36.9 | 0.3 | 13.3 | 12 | 6 | 999 | -24.87 |  | Open Full
GV24 |  | 52.3 | 35.9 | 0.2 | 11.6 | 8 | 6 | 999 | -24.36 |  | Open Full
GV25 |  | 41 | 36 | 1.4 | 21.6 | 4 | 5 | 999 | -0.58 |  | Left Closed
GV26 + 27 Manifold |  | 52.6 | 38 | 0.4 | 9 | 5 | 8 | 999 | -24.89 |  | Open Full
GV28+ 29 Manifold |  | 51.9 | 38 | 0.6 | 9.5 | 8 | 5 | 999 | -24.56 |  | Open Full
GV26 |  | 53 | 37.6 | 0.3 | 9.1 | 5 | 4 | 999 | -24.99 |  | Open Full
GV27 |  | 51.8 | 38.8 | 0.5 | 8.9 | 6 | 6 | 999 | -24.74 |  | Open Full
GV28 |  | 52.2 | 37.5 | 0.4 | 9.9 | 9 | 9 | 999 | -24.65 |  | Open Full
GV29 |  | 50.1 | 38.2 | 0.7 | 11 | 2 | 2 | 999 | -24.38 |  | Open Full
GVA |  | 33.9 | 28.7 | 5.2 | 32.2 | 2 | 2 | 999 | -0.56 |  | Off Low gas
B+C Manifold |  | 50.2 | 37.2 | 0.3 | 12.3 | 7 | 7 | 999 | -24.55 |  | Open Full
GV B |  | 50.6 | 36.2 | 0.5 | 12.7 | 5 | 5 | 999 | -24.59 |  | Open Full
GV C |  | 50 | 37.8 | 0.2 | 12 | 10 | 9 | 999 | -24.41 |  | Open Full
GV30 |  | 46.5 | 36.2 | 1.1 | 16.2 | 11 | 1 | 999 | -6.58 |  | Left Cracked
GV31 |  | 45.2 | 36.7 | 1.2 | 16.9 | 4 | 2 | 999 | -6.41 |  | Cracked Open
GV32 |  | 46 | 36.1 | 1.1 | 16.8 | 9 | 5 | 999 | -6.39 |  | Cracked Open
GV33 |  | 44.8 | 36.5 | 1.1 | 17.6 | 7 | 11 | 999 | -6.87 |  | Cracked Open
GV34 |  | 45.2 | 37 | 1.2 | 16.6 | 5 | 8 | 999 | -6.44 |  | Cracked Open
GV 35 (New Well) |  | 21.9 | 25.3 | 1.7 | 51.1 | 8 | 8 | 999 | -1.11 |  | Left Closed
GV 36 (New Well) |  | 24.8 | 23.9 | 4.5 | 46.8 | 5 | 8 | 999 | -1.34 |  | OFF low gas.
GV 37 (New Well) |  | 51.2 | 37.9 | 0.1 | 10.8 | 4 | 7 | 999 | -24.58 |  | Left open Full
GV 38 (New Well) |  | 46.2 | 36 | 1.1 | 16.7 | 9 | 5 | 999 | -7.01 |  | Cracked Open
GV 39 (New Well) |  | 45.5 | 36.8 | 1.5 | 16.2 | 14 | 6 | 999 | -6.51 |  | Cracked Open (High o2)
GV 40 (New Well) |  | 45 | 36.4 | 1.1 | 17.5 | 18 | 9 | 999 | -6.43 |  | Cracked Open
GV 41 (New Well) |  | 45.5 | 36.5 | 1.2 | 16.8 | 13 | 6 | 999 | -6.38 |  | Cracked Open
GV 42 (New Well) |  | 39.9 | 36.2 | 1.2 | 22.7 | 14 | 4 | 999 | -1.21 |  | Off Low Gas
GV 43 (New Well) |  | 46.5 | 35.4 | 1.1 | 17 | 9 | 1 | 999 | -6.39 |  | Cracked open
GV 44 (New Well) |  | 40 | 36.5 | 1.3 | 22.2 | 11 | 2 | 999 | -0.89 |  | Off Low gas
GV 45 (New Well) |  | 45.9 | 36 | 1.2 | 16.9 | 9 | 12 | 999 | -6.11 |  | Cracked Open
GV 46 (New Well) |  | 50 | 38 | 0.3 | 11.7 | 7 | 11 | 999 | -24.58 |  | Open Full
GV 47 (New Well) |  | 45.8 | 36.5 | 1.2 | 16.5 | 9 | 1 | 999 | -6.89 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 8 | 8 | 999 | -24.78 |  | Open Full
GV 49 (New Well) |  | 46 | 36 | 1.2 | 16.8 | 8 | 6 | 999 | -6.25 |  | Cracked open
LC1B |  | 35.9 | 32.2 | 1.9 | 30 | 4 | 9 | 999 | -1.24 |  | OFF
LC2R? |  | 51.2 | 36.9 | 0.2 | 11.7 | 5 | 8 | 999 | -24.78 |  | Open Full
GV 2.1 |  | 50.4 | 38 | 0.3 | 11.3 | 13 | 8 | 999 | -24.63 |  | Open Full
GV 2.2+ LC2B MAN |  | 47.9 | 36.8 | 1.1 | 14.2 | 11 | 5 | 999 | -7.89 |  | Cracked Open at Manifold
GV 2.2 |  | 47.4 | 37.2 | 1 | 14.4 | 13 | 7 | 999 | -8 |  | Cracked Open
LC2B |  | 48.3 | 36.2 | 1.3 | 14.2 | 8 | 2 | 999 | -7.82 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 48 | 37 | 1 | 14 | 5 | 7 | 999 | -13.41 |  | Left Open Half Way
LC3.1 |  | 48 | 37 | 1 | 14 | 5 | 7 | 999 | -13.41 |  | Left open half way
LC3 |  | 45.9 | 34.2 | 2.5 | 17.4 | 17 | 2 | 999 | -0.39 |  | OFF
LC4B |  | 47.5 | 36.2 | 1.1 | 15.2 | 11 | 1 | 999 | -7.01 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.9 | 37.2 | 0.7 | 13.2 | 8 | 9 | 999 | -24.58 |  | Open Full
R1 |  | 46.2 | 36.9 | 1.1 | 15.8 | 7 | 6 | 999 | -9.23 |  | Cracked Open
R1B |  | 50.4 | 38 | 0.4 | 11.2 | 11 | 16 | 999 | -25.11 |  | Open Full
R2B |  | 48.7 | 37.8 | 0.6 | 12.9 | 15 | 5 | 999 | -24.79 |  | Open Full
R4B |  | 41 | 35.2 | 3.9 | 19.9 | 4 | 8 | 999 | -0.32 |  | Left closed
R6B |  | 51.2 | 38 | 0.3 | 10.5 | 8 | 11 | 999 | -24.57 |  | Open Full
LC5 |  | 47.5 | 35 | 2.6 | 14.9 | 7 | 3 | 999 | -0.36 |  | Left Off ( Gas drops quick)
LC6 |  | 46.3 | 34.9 | 2.9 | 15.9 | 12 | 6 | 999 | -0.57 |  | Left Off ( Gas drops quick)
LC6B |  | 50.8 | 36.4 | 0.5 | 12.3 | 8 | 8 | 999 | -24.59 |  | Open Full
PW1 |  | 2 | 0.7 | 13.8 | 83.5 | 11 | 5 | 999 | -0.46 |  | Left Off
PW2 |  | 34.9 | 19.5 | 2.9 | 42.7 | 4 | 4 | 999 | 0.36 |  | Left Off
PW3 |  | 35.8 | 20 | 3.2 | 41 | 14 | 1 | 999 | 0.24 |  | Left Off
PW4 |  | 47 | 36.5 | 1.4 | 15.1 | 8 | 13 | 999 | -6.04 |  | Cracked Open
PW5 |  | 35.8 | 26.2 | 1.4 | 36.6 | 6 | 8 | 999 | -0.56 |  | Left Off
PW6 |  | 33.7 | 27 | 2.6 | 36.7 | 8 | 9 | 999 | -0.62 |  | Left Off
Flare | 15:20 | 51.2 | 38.3 | 0.4 | 10.1 | 14 | 5 | 999 | 170 |  | Engine Off (Awaiting new engine) Flaring Running 400 KW/H
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## February 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-02-02
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 7 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:48 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 997 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:53 | 0.2 | 1.4 | 19.6 | 78.8 | 0 | 0 | 997 | 0.41 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:54 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 997 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:56 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 997 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:00 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 997 | 0.26 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:04 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 997 | 0.45 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:07 | 28 | 1.8 | 19.7 | 50.5 | 0 | 0 | 997 | -0.12 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:13 | 28.2 | 2.6 | 20.1 | 49.1 | 0 | 0 | 997 | 0.36 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:18 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 997 | -0.15 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:30 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 997 | 0.73 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:34 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 997 | -0.42 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:38 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 997 | 0.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:41 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 997 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:44 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 997 | 0.74 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:47 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 997 | 0.23 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:54 | 0.2 | 2.3 | 19.5 | 78 | 0 | 0 | 997 | -0.18 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:20 | 0.3 | 2 | 19.9 | 77.8 | 0 | 0 | 997 | 0.92 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:24 | 0 | 3 | 20 | 77 | 0 | 0 | 997 | 0.37 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:27 | 0.2 | 1.6 | 19.3 | 78.9 | 0 | 0 | 997 | -0.18 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:32 | 0.3 | 2.7 | 19.7 | 77.3 | 0 | 0 | 997 | 0.29 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:37 | 0 | 3 | 19.5 | 77.5 | 0 | 0 | 997 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:40 | 0 | 0.8 | 19.2 | 80 | 0 | 0 | 997 | 0.54 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:44 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 997 | 0.87 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-02-09
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:10 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1000 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:15 | 0.1 | 1.6 | 19.7 | 78.6 | 0 | 0 | 1000 | 0.23 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:18 | 0 | 1 | 20 | 79 | 0 | 0 | 1000 | 0.12 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:20 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 1000 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:22 | 0 | 0.9 | 19.8 | 79.3 | 0 | 0 | 1000 | 0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:26 | 0 | 2.3 | 19.2 | 78.5 | 0 | 0 | 1000 | -0.45 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:29 | 28.9 | 1.5 | 19.9 | 49.7 | 0 | 0 | 1000 | 0.68 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:35 | 29.1 | 2.5 | 20 | 48.4 | 0 | 0 | 1000 | -0.19 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:40 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1000 | 0.38 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:52 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1000 | -0.45 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:56 | 0 | 1.9 | 19.7 | 78.4 | 0 | 0 | 1000 | -0.62 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:00 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1000 | 0.54 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:03 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1000 | -0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:06 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1000 | 0.62 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:09 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1000 | -0.38 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:16 | 0.3 | 2.6 | 20 | 77.1 | 0 | 0 | 1000 | -0.42 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:42 | 0.5 | 2.4 | 20.1 | 77 | 0 | 0 | 1000 | 0.28 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:46 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 1000 | -0.58 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:49 | 0.4 | 1.8 | 19.6 | 78.2 | 0 | 0 | 1000 | -0.36 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:54 | 0.2 | 3.1 | 19.9 | 76.8 | 0 | 0 | 1000 | -0.89 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:59 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 1000 | 0.27 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:02 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1000 | -0.24 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:06 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1000 | -0.28 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-02-16
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 10 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:58 | 0 | 1 | 20 | 79 | 0 | 0 | 999 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:03 | 0.2 | 1.5 | 19.6 | 78.7 | 0 | 0 | 999 | -0.36 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:04 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 999 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:06 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 999 | 0.91 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:10 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 999 | 0.95 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:14 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | -0.63 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:17 | 28.5 | 1.8 | 20 | 49.7 | 0 | 0 | 999 | 0.25 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:23 | 28.7 | 2.2 | 19.6 | 49.5 | 0 | 0 | 999 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:28 | 0 | 1.7 | 19.2 | 79.1 | 0 | 0 | 999 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:40 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 999 | -0.65 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:44 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 999 | 0.32 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:48 | 0 | 1.8 | 19.2 | 79 | 0 | 0 | 999 | -0.17 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:51 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 999 | 0.36 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:54 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 999 | -0.98 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:57 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 999 | 0.25 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:04 | 0.2 | 2.5 | 20.3 | 77 | 0 | 0 | 999 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:30 | 0.3 | 2.8 | 20 | 76.9 | 0 | 0 | 999 | 0.75 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:34 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 999 | 0.36 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:37 | 0.2 | 1.7 | 19.5 | 78.6 | 0 | 0 | 999 | -0.82 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:42 | 0.1 | 3 | 19.7 | 77.2 | 0 | 0 | 999 | 0.39 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:47 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 999 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:50 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | 0.27 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:54 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 999 | -0.54 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-02-23
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 11 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:23 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 1002 | -0.53 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:28 | 0.3 | 1.4 | 20 | 78.3 | 0 | 0 | 1002 | 0.42 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:30 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1002 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1002 | -0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:35 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | -0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:39 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.64 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:42 | 28 | 1.6 | 19.8 | 50.6 | 0 | 0 | 1002 | 0.29 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:48 | 28.1 | 2.2 | 19.9 | 49.8 | 0 | 0 | 1002 | -0.15 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:53 | 0 | 1.9 | 19.6 | 78.5 | 0 | 0 | 1002 | 0.36 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:05 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | -0.52 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:09 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 1002 | 0.14 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:13 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 1002 | -0.78 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:16 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | 0.96 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:19 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 1002 | 0.32 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:22 | 0 | 2.5 | 19.3 | 78.2 | 0 | 0 | 1002 | -0.14 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:29 | 0.4 | 2.6 | 19.9 | 77.1 | 0 | 0 | 1002 | 0.25 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:55 | 0.1 | 3 | 20.1 | 76.8 | 0 | 0 | 1002 | -0.78 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:59 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 1002 | 0.63 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:02 | 0.3 | 1.5 | 19.9 | 78.3 | 0 | 0 | 1002 | 0.87 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:07 | 0.2 | 2.8 | 20 | 77 | 0 | 0 | 1002 | 0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:12 | 0 | 2.9 | 19.7 | 77.4 | 0 | 0 | 1002 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:15 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1002 | 0.54 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:19 | 0 | 2.2 | 19.3 | 78.5 | 0 | 0 | 1002 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-02-08
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 8 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 12:00 | 53.6 | 37.4 | 0.3 | 8.7 | 4 | 5 | 1004 | 180 |  | Flare On 400 KWH
GV1 |  | 32.8 | 26.9 | 1.2 | 39.1 | 6 | 6 | 1004 | -0.21 |  | OFF
GV3 |  | 52 | 36.9 | 0.2 | 10.9 | 5 | 7 | 1004 | -25.56 |  | Open Full
GV4 |  | 45.6 | 36 | 1 | 17.4 | 8 | 8 | 1004 | -6.99 |  | Cracked Open
GV6 |  | 45.8 | 37 | 1.1 | 16.1 | 4 | 5 | 1004 | -6.87 |  | Cracked Open
GV7 |  | 33.9 | 31.9 | 2.6 | 31.6 | 6 | 4 | 1004 | -0.11 |  | Off Low Gas high o2
GV8 |  | 37.5 | 34.5 | 2.9 | 25.1 | 2 | 9 | 1004 | -0.08 |  | Off Low Gas high o3
GV9 |  | 51.2 | 37.8 | 0.3 | 10.7 | 3 | 8 | 1004 | -26.01 |  | Open Full
GV10 |  | 38.7 | 35.9 | 1.5 | 23.9 | 5 | 5 | 1004 | -0.04 |  | Off
GV11 |  | 45.8 | 34.5 | 1 | 18.7 | 6 | 2 | 1004 | -7.02 |  | Cracked Open
GV12+R3 Manifold |  | 51.2 | 37.1 | 0.4 | 11.3 | 3 | 6 | 1004 | -25.99 |  | Open Full
GV12 |  | 51.6 | 37.5 | 0.5 | 10.4 | 2 | 7 | 1004 | -26.21 |  | Open Full
R3 |  | 50.2 | 36.2 | 0.3 | 13.3 | 1 | 4 | 1004 | -25.87 |  | Open Full
GV13 |  | 2.2 | 3.6 | 19.9 | 74.3 | 6 | 6 | 1004 | -0.23 |  | Left Closed
GV14 |  | 50 | 36.5 | 0.4 | 13.1 | 7 | 8 | 1004 | -25.89 |  | Open Full
GV15 |  | 50.2 | 37 | 0.2 | 12.6 | 5 | 9 | 1004 | -26.03 |  | Open Full
GV16 |  | 46.2 | 35 | 1.1 | 17.7 | 6 | 7 | 1004 | -7.02 |  | Left Cracked
GV17+LC4 Manifold |  | 46.2 | 36.1 | 2.5 | 15.2 | 8 | 6 | 1004 | -0.11 |  | Off at Manifold Gas drops quick.
GV17 |  | 45.5 | 36.5 | 2.2 | 15.8 | 9 | 4 | 1004 | -0.15 |  | Open Full at Well
LC4 |  | 47 | 35.8 | 2.8 | 14.4 | 6 | 9 | 1004 | -0.1 |  | Open Full at well
GV18 |  | 51.2 | 37.8 | 0.3 | 10.7 | 8 | 5 | 1004 | -25.78 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.2 | 37.5 | 1.6 | 14.7 | 3 | 6 | 1004 | -0.88 |  | Off gas drops off quick.
GV23 |  | 50.2 | 37.5 | 0.4 | 11.9 | 7 | 8 | 1004 | -25.55 |  | Open Full
GV24 |  | 51.8 | 36.2 | 0.2 | 11.8 | 9 | 7 | 1004 | -25.87 |  | Open Full
GV25 |  | 40.8 | 36.8 | 1.5 | 20.9 | 6 | 4 | 1004 | -0.56 |  | Left Closed
GV26 + 27 Manifold |  | 53 | 37.9 | 0.2 | 8.9 | 8 | 6 | 1004 | -26.02 |  | Open Full
GV28+ 29 Manifold |  | 52.1 | 38.2 | 0.4 | 9.3 | 7 | 6 | 1004 | -26.14 |  | Open Full
GV26 |  | 53.6 | 37.5 | 0.2 | 8.7 | 6 | 5 | 1004 | -25.89 |  | Open Full
GV27 |  | 52.4 | 38.2 | 0.2 | 9.2 | 9 | 7 | 1004 | -26.21 |  | Open Full
GV28 |  | 52.4 | 37.8 | 0.5 | 9.3 | 5 | 7 | 1004 | -26.33 |  | Open Full
GV29 |  | 51.8 | 38.5 | 0.3 | 9.4 | 8 | 4 | 1004 | -25.95 |  | Open Full
GVA |  | 34.5 | 29.8 | 5 | 30.7 | 3 | 5 | 1004 | -0.02 |  | Off Low gas
B+C Manifold |  | 50.7 | 37.5 | 0.4 | 11.4 | 5 | 6 | 1004 | -25.55 |  | Open Full
GV B |  | 50.9 | 36.9 | 0.4 | 11.8 | 3 | 4 | 1004 | -25.49 |  | Open Full
GV C |  | 50.1 | 37.8 | 0.3 | 11.8 | 7 | 7 | 1004 | -25.69 |  | Open Full
GV30 |  | 47 | 36.9 | 1.1 | 15 | 8 | 8 | 1004 | -6.49 |  | Left Cracked
GV31 |  | 46.2 | 35.8 | 1 | 17 | 7 | 5 | 1004 | -6.89 |  | Cracked Open
GV32 |  | 46.2 | 36.5 | 1 | 16.3 | 9 | 6 | 1004 | -6.84 |  | Cracked Open
GV33 |  | 45.8 | 37.8 | 1.1 | 15.3 | 8 | 5 | 1004 | -6.92 |  | Cracked Open
GV34 |  | 46.9 | 36.9 | 1.1 | 15.1 | 6 | 4 | 1004 | -6.89 |  | Cracked Open
GV 35 (New Well) |  | 22.9 | 26.9 | 2 | 48.2 | 4 | 7 | 1004 | -0.58 |  | Left Closed
GV 36 (New Well) |  | 25.8 | 24.5 | 4.6 | 45.1 | 2 | 5 | 1004 | -0.57 |  | OFF low gas.
GV 37 (New Well) |  | 52.2 | 38 | 0.3 | 9.5 | 7 | 8 | 1004 | -25.99 |  | Left open Full
GV 38 (New Well) |  | 46.8 | 36.8 | 1.1 | 15.3 | 8 | 2 | 1004 | -7.06 |  | Cracked Open
GV 39 (New Well) |  | 45.9 | 36.5 | 1.2 | 16.4 | 6 | 3 | 1004 | -6.89 |  | Cracked Open
GV 40 (New Well) |  | 46.1 | 36.9 | 1 | 16 | 5 | 4 | 1004 | -6.74 |  | Cracked Open
GV 41 (New Well) |  | 46 | 37 | 1.1 | 15.9 | 2 | 5 | 1004 | -6.55 |  | Cracked Open
GV 42 (New Well) |  | 40 | 37.2 | 1.6 | 21.2 | 3 | 6 | 1004 | -0.98 |  | Off Low Gas
GV 43 (New Well) |  | 45.9 | 36 | 1.1 | 17 | 2 | 8 | 1004 | -7.08 |  | Cracked open
GV 44 (New Well) |  | 39.8 | 37.9 | 1.4 | 20.9 | 9 | 7 | 1004 | -0.22 |  | Off Low gas
GV 45 (New Well) |  | 45.5 | 36.9 | 1 | 16.6 | 6 | 8 | 1004 | -7.09 |  | Cracked Open
GV 46 (New Well) |  | 50.8 | 37.6 | 0.4 | 11.2 | 5 | 6 | 1004 | -25.69 |  | Open Full
GV 47 (New Well) |  | 46 | 36.9 | 1.1 | 16 | 4 | 3 | 1004 | -7.14 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 7 | 4 | 1004 | -25.87 |  | Open Full
GV 49 (New Well) |  | 47.4 | 36.9 | 1.2 | 14.5 | 4 | 5 | 1004 | -6.87 |  | Cracked open
LC1B |  | 37.8 | 33.3 | 1.5 | 27.4 | 5 | 6 | 1004 | -1 |  | OFF
LC2R? |  | 50.8 | 37 | 0.1 | 12.1 | 5 | 7 | 1004 | -25.54 |  | Open Full
GV 2.1 |  | 51.9 | 38.2 | 0.4 | 9.5 | 9 | 6 | 1004 | -26.32 |  | Open Full
GV 2.2+ LC2B MAN |  | 47 | 37.5 | 1.2 | 14.3 | 8 | 6 | 1004 | -7.45 |  | Cracked Open at Manifold
GV 2.2 |  | 47.2 | 37.8 | 0.9 | 14.1 | 6 | 7 | 1004 | -8.01 |  | Cracked Open
LC2B |  | 46.5 | 36.9 | 1.2 | 15.4 | 10 | 5 | 1004 | -7.12 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.2 | 36.9 | 1.1 | 14.8 | 4 | 8 | 1004 | -12.99 |  | Left Open Half Way
LC3.1 |  | 47.2 | 36.9 | 1.1 | 14.8 | 4 | 8 | 1004 | -12.99 |  | Left open half way
LC3 |  | 42.1 | 35 | 2.9 | 20 | 4 | 3 | 1004 | -0.45 |  | OFF
LC4B |  | 46.2 | 36.5 | 1.1 | 16.2 | 8 | 4 | 1004 | -6.09 |  | Left Cracked Open
R1 + R1B Manifold |  | 49 | 37.2 | 0.8 | 13 | 6 | 7 | 1004 | -24.89 |  | Open Full
R1 |  | 47.1 | 37.5 | 1 | 14.4 | 4 | 6 | 1004 | -10.21 |  | Cracked Open
R1B |  | 52.6 | 36.9 | 0.5 | 10 | 8 | 8 | 1004 | -26.23 |  | Open Full
R2B |  | 49.8 | 36.8 | 0.5 | 12.9 | 6 | 7 | 1004 | -26.99 |  | Open Full
R4B |  | 42.8 | 36.9 | 3.5 | 16.8 | 8 | 8 | 1004 | -0.21 |  | Left closed
R6B |  | 52.1 | 37.9 | 0.4 | 9.6 | 7 | 5 | 1004 | -25.89 |  | Open Full
LC5 |  | 47.6 | 34.7 | 2.8 | 14.9 | 8 | 6 | 1004 | -0.39 |  | Left Off ( Gas drops quick)
LC6 |  | 48 | 35.9 | 2.7 | 13.4 | 9 | 5 | 1004 | -0.01 |  | Left Off ( Gas drops quick)
LC6B |  | 51.7 | 35.9 | 0.4 | 12 | 3 | 5 | 1004 | -25.77 |  | Open Full
PW1 |  | 2.6 | 0.9 | 12.6 | 83.9 | 1 | 4 | 1004 | -0.59 |  | Left Off
PW2 |  | 35.7 | 20.1 | 2.5 | 41.7 | 4 | 9 | 1004 | -0.47 |  | Left Off
PW3 |  | 36.2 | 19.9 | 3.9 | 40 | 5 | 5 | 1004 | 0.36 |  | Left Off
PW4 |  | 46.9 | 35.8 | 1.2 | 16.1 | 95 | 2 | 1004 | -6.62 |  | Cracked Open
PW5 |  | 36.4 | 28.7 | 1.6 | 33.3 | 8 | 3 | 1004 | -0.01 |  | Left Off
PW6 |  | 33.1 | 25.9 | 3 | 38 | 7 | 5 | 1004 | -0.08 |  | Left Off
Flare | 15:20 | 53.1 | 37.9 | 0.3 | 8.7 | 4 | 6 | 1004 | 180 |  | Engine Off (Awaiting new engine) Flaring Running 400 KW/H
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## March 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-03-02
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 13 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 996 | 0.53 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.2 | 1.2 | 19.8 | 78.8 | 0 | 0 | 996 | -0.51 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:30 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 996 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 996 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 996 | 0.57 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 996 | 0.53 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 28.6 | 1.5 | 19.5 | 50.4 | 0 | 0 | 996 | 0.48 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:46 | 28.3 | 2 | 19.6 | 50.1 | 0 | 0 | 996 | 0.6 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 996 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 996 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 996 | 0.33 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:12 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 996 | -0.66 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 996 | 0.39 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 2.5 | 19.5 | 78 | 0 | 0 | 996 | 0.41 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 996 | 0.88 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.3 | 2.8 | 19.8 | 77.1 | 0 | 0 | 996 | 0.46 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.2 | 2.8 | 20 | 77 | 0 | 0 | 996 | -0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 996 | 0.45 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.2 | 1.7 | 19.7 | 78.4 | 0 | 0 | 996 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.3 | 2.5 | 19.9 | 77.3 | 0 | 0 | 996 | 0.46 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 996 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 996 | -0.66 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 996 | 0.41 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-03-09
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:19 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | 0.66 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:24 | 0.3 | 1 | 20 | 78.7 | 0 | 0 | 1002 | -0.56 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:25 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1002 | 0.35 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:27 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1002 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:31 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | 0.62 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:35 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1002 | 0.62 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:38 | 28.4 | 1.6 | 19.8 | 50.2 | 0 | 0 | 1002 | 0.55 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:44 | 28 | 1.8 | 19.6 | 50.6 | 0 | 0 | 1002 | 0.63 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:49 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.74 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:01 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | -0.49 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:05 | 0 | 2.2 | 19.7 | 78.1 | 0 | 0 | 1002 | 0.3 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:09 | 0 | 2.7 | 19.6 | 77.7 | 0 | 0 | 1002 | -0.71 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:12 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | 0.4 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:15 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 1002 | 0.44 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:18 | 0 | 2.5 | 19.4 | 78.1 | 0 | 0 | 1002 | 0.93 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:25 | 0.2 | 2.9 | 19.9 | 77 | 0 | 0 | 1002 | 0.5 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:51 | 0.3 | 2.5 | 19.9 | 77.3 | 0 | 0 | 1002 | -0.53 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:55 | 0 | 3.2 | 20 | 76.8 | 0 | 0 | 1002 | 0.5 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:58 | 0.3 | 1.5 | 19.5 | 78.7 | 0 | 0 | 1002 | 0.59 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:03 | 0.2 | 2.8 | 20 | 77 | 0 | 0 | 1002 | 0.44 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:08 | 0 | 2.7 | 19.3 | 78 | 0 | 0 | 1002 | 0.78 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:11 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1002 | -0.78 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:15 | 0 | 2.2 | 20 | 77.8 | 0 | 0 | 1002 | 0.45 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-03-16
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:45 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:50 | 0.3 | 1.2 | 19.9 | 78.6 | 0 | 0 | 1002 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:51 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1002 | 0.42 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:53 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 1002 | -0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:57 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:01 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1002 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:04 | 28.1 | 1.8 | 19.8 | 50.3 | 0 | 0 | 1002 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:10 | 28.2 | 1.5 | 19.9 | 50.4 | 0 | 0 | 1002 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:15 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1002 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:27 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 1002 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:31 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1002 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:35 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 1002 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:38 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1002 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:41 | 0 | 2 | 20 | 78 | 0 | 0 | 1002 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:44 | 0 | 2.8 | 19.6 | 77.6 | 0 | 0 | 1002 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:51 | 0.4 | 3.2 | 20.1 | 76.3 | 0 | 0 | 1002 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:17 | 0.3 | 2.4 | 19.6 | 77.7 | 0 | 0 | 1002 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:21 | 0 | 3.5 | 19.8 | 76.7 | 0 | 0 | 1002 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:24 | 0.3 | 1.4 | 20.1 | 78.2 | 0 | 0 | 1002 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:29 | 0.2 | 3 | 19.8 | 77 | 0 | 0 | 1002 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:34 | 0 | 2.9 | 19.5 | 77.6 | 0 | 0 | 1002 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:37 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:41 | 0 | 2.6 | 20.1 | 77.3 | 0 | 0 | 1002 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-03-23
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 2017-03-29
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:36 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1005 | -0.63 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:41 | 0.4 | 1.4 | 20.1 | 78.1 | 0 | 0 | 1005 | -0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:43 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1005 | -0.35 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:45 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 1005 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:48 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1005 | -0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:52 | 0 | 2.7 | 19.7 | 77.6 | 0 | 0 | 1005 | 0.35 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:55 | 28.3 | 1.6 | 19.9 | 50.2 | 0 | 0 | 1005 | -0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:01 | 27.9 | 1.4 | 20 | 50.7 | 0 | 0 | 1005 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:06 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1005 | 0.38 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:18 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1005 | -0.96 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:22 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 1005 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:26 | 0 | 3.2 | 19.5 | 77.3 | 0 | 0 | 1005 | 0.24 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:29 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1005 | -0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:32 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1005 | 0.38 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:35 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 1005 | -0.77 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:42 | 0.3 | 3 | 19.9 | 76.8 | 0 | 0 | 1005 | -0.65 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:08 | 0.2 | 2.6 | 19.7 | 77.5 | 0 | 0 | 1005 | -78 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:12 | 0 | 3.3 | 19.6 | 77.1 | 0 | 0 | 1005 | 0.63 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:15 | 0.4 | 1.6 | 19.8 | 78.2 | 0 | 0 | 1005 | -0.87 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:20 | 0.3 | 2.7 | 20 | 77 | 0 | 0 | 1005 | -0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:25 | 0 | 3.2 | 19.6 | 77.2 | 0 | 0 | 1005 | -0.48 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:28 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 1005 | -0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:32 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 1005 | 0.86 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-03-30
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/09//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:23 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1001 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:28 | 0.3 | 1.2 | 19.9 | 78.6 | 0 | 0 | 1001 | 0.38 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:29 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1001 | 0.48 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1001 | -0.58 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:35 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1001 | 0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:39 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1001 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:42 | 28.1 | 1.2 | 19.8 | 50.9 | 0 | 0 | 1001 | 0.58 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:48 | 28 | 1.6 | 19.6 | 50.8 | 0 | 0 | 1001 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:53 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 1001 | 0.68 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:05 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1001 | 0.87 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:09 | 0 | 2.6 | 19.6 | 77.8 | 0 | 0 | 1001 | 0.59 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:13 | 0 | 3.5 | 20.1 | 76.4 | 0 | 0 | 1001 | 0.23 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:16 | 0 | 1.4 | 20.2 | 78.4 | 0 | 0 | 1001 | 0.87 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:19 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1001 | -0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:22 | 0 | 2.7 | 19.9 | 77.4 | 0 | 0 | 1001 | 0.23 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:29 | 0.4 | 2.4 | 20.1 | 77.1 | 0 | 0 | 1001 | -0.46 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:55 | 0.2 | 2.9 | 19.6 | 77.3 | 0 | 0 | 1001 | 0.68 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:59 | 0 | 3.2 | 19.9 | 76.9 | 0 | 0 | 1001 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:02 | 0.3 | 1.9 | 20 | 77.8 | 0 | 0 | 1001 | -0.15 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:07 | 0.2 | 2.8 | 19.6 | 77.4 | 0 | 0 | 1001 | 0.24 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:12 | 0 | 3 | 19.5 | 77.5 | 0 | 0 | 1001 | 0.25 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:15 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1001 | -0.78 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:19 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 1001 | 0.52 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-03-13
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 12 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 11:40 | 54 | 37.9 | 0.4 | 7.7 | 5 | 8 | 999 | 175 |  | Flare On 400 KWH
GV1 |  | 33.8 | 27.5 | 1.4 | 37.3 | 8 | 6 | 999 | -0.21 |  | OFF
GV3 |  | 52.6 | 37.8 | 0.2 | 9.4 | 6 | 5 | 999 | -27.55 |  | Open Full
GV4 |  | 48.5 | 37.5 | 0.7 | 13.3 | 11 | 6 | 999 | -6.99 | -10.25 | Reg Opened Half Way
GV6 |  | 46.5 | 36.5 | 1.2 | 15.8 | 8 | 3 | 999 | -6.58 |  | Cracked Open
GV7 |  | 34.5 | 31.4 | 2.5 | 31.6 | 9 | 7 | 999 | -0.05 |  | Off Low Gas high o2
GV8 |  | 37.8 | 35 | 2.4 | 24.8 | 7 | 8 | 999 | -0.2 |  | Off Low Gas high o3
GV9 |  | 51.4 | 36.9 | 0.2 | 11.5 | 4 | 11 | 999 | -27.65 |  | Open Full
GV10 |  | 38.9 | 36.2 | 1.4 | 23.5 | 1 | 5 | 999 | -0.01 |  | Off
GV11 |  | 47.9 | 35.5 | 1 | 15.6 | 9 | 6 | 999 | -7.11 | -11.06 | Reg Opened Hald way
GV12+R3 Manifold |  | 51.5 | 37.3 | 0.3 | 10.9 | 4 | 4 | 999 | -27.54 |  | Open Full
GV12 |  | 51.9 | 37.8 | 0.4 | 9.9 | 5 | 6 | 999 | -27.34 |  | Open Full
R3 |  | 50.9 | 36.8 | 0.2 | 12.1 | 3 | 3 | 999 | -27.69 |  | Open Full
GV13 |  | 2.6 | 3.9 | 19.5 | 74 | 6 | 8 | 999 | -0.4 |  | Left Closed
GV14 |  | 50.8 | 37 | 0.5 | 11.7 | 10 | 10 | 999 | -27.19 |  | Open Full
GV15 |  | 51.2 | 36.9 | 0.1 | 11.8 | 9 | 9 | 999 | -27.53 |  | Open Full
GV16 |  | 48 | 36.2 | 0.9 | 14.9 | 7 | 6 | 999 | -7.45 | -9.23 | Reg Opened slightly more
GV17+LC4 Manifold |  | 46.5 | 35.8 | 2.4 | 15.3 | 5 | 7 | 999 | -0.06 |  | Off at Manifold Gas drops quick.
GV17 |  | 45.8 | 36.7 | 2 | 15.5 | 6 | 4 | 999 | -0.09 |  | Open Full at Well
LC4 |  | 47.2 | 35.6 | 3 | 14.2 | 5 | 8 | 999 | -0.03 |  | Open Full at well
GV18 |  | 51.5 | 37.6 | 0.4 | 10.5 | 7 | 6 | 999 | -27.47 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.5 | 37.2 | 1.2 | 15.1 | 7 | 9 | 999 | -0.56 |  | Off gas drops off quick.
GV23 |  | 51.2 | 37.2 | 0.3 | 11.3 | 10 | 10 | 999 | -27.49 |  | Open Full
GV24 |  | 52.3 | 37.5 | 0.5 | 9.7 | 9 | 6 | 999 | -27.93 |  | Open Full
GV25 |  | 41.9 | 36 | 1.6 | 20.5 | 7 | 5 | 999 | -0.23 |  | Left Closed
GV26 + 27 Manifold |  | 52.5 | 37.6 | 0.3 | 9.6 | 9 | 5 | 999 | -27.45 |  | Open Full
GV28+ 29 Manifold |  | 52.6 | 38.5 | 0.5 | 8.4 | 10 | 8 | 999 | -27.52 |  | Open Full
GV26 |  | 53.2 | 37.4 | 0.2 | 9.2 | 8 | 5 | 999 | -27.39 |  | Open Full
GV27 |  | 52.1 | 38 | 0.4 | 9.5 | 10 | 6 | 999 | -27.61 |  | Open Full
GV28 |  | 53 | 38 | 0.5 | 8.5 | 7 | 9 | 999 | -27.48 |  | Open Full
GV29 |  | 51.9 | 38.9 | 0.5 | 8.7 | 11 | 6 | 999 | -27.58 |  | Open Full
GVA |  | 35.6 | 30.2 | 4.5 | 29.7 | 5 | 6 | 999 | 0 |  | Off Low gas
B+C Manifold |  | 51.2 | 37.2 | 0.3 | 11.3 | 6 | 5 | 999 | -27.49 |  | Open Full
GV B |  | 51.4 | 36.8 | 0.4 | 11.4 | 6 | 7 | 999 | -27.38 |  | Open Full
GV C |  | 50.4 | 37.5 | 0.3 | 11.8 | 8 | 3 | 999 | -27.7 |  | Open Full
GV30 |  | 47.5 | 36.8 | 1.1 | 14.6 | 9 | 7 | 999 | -6.85 |  | Left Cracked
GV31 |  | 46.8 | 36.7 | 1.1 | 15.4 | 8 | 7 | 999 | -6.99 |  | Cracked Open
GV32 |  | 46.7 | 36.9 | 1 | 15.4 | 6 | 9 | 999 | -6.78 |  | Cracked Open
GV33 |  | 46.2 | 36.8 | 1.1 | 15.9 | 9 | 8 | 999 | -6.54 |  | Cracked Open
GV34 |  | 47.1 | 37.9 | 1.2 | 13.8 | 10 | 6 | 999 | -6.93 |  | Cracked Open
GV 35 (New Well) |  | 23.9 | 27.8 | 1.8 | 46.5 | 11 | 9 | 999 | -0.98 |  | Left Closed
GV 36 (New Well) |  | 26.9 | 25.6 | 4.4 | 43.1 | 6 | 7 | 999 | 0 |  | OFF low gas.
GV 37 (New Well) |  | 53.9 | 38.2 | 0.4 | 7.5 | 5 | 6 | 999 | -26.99 |  | Left open Full
GV 38 (New Well) |  | 47 | 37.5 | 1.2 | 14.3 | 9 | 9 | 999 | -7.45 |  | Cracked Open
GV 39 (New Well) |  | 46.5 | 36.9 | 1 | 15.6 | 6 | 8 | 999 | -6.88 |  | Cracked Open
GV 40 (New Well) |  | 46.2 | 37 | 1 | 15.8 | 8 | 4 | 999 | -6.81 |  | Cracked Open
GV 41 (New Well) |  | 46.5 | 36.9 | 1.1 | 15.5 | 5 | 1 | 999 | -6.54 |  | Cracked Open
GV 42 (New Well) |  | 41.6 | 37.5 | 1.5 | 19.4 | 6 | 8 | 999 | -0.54 |  | Off Low Gas
GV 43 (New Well) |  | 46.3 | 36.5 | 1 | 16.2 | 9 | 6 | 999 | -6.89 |  | Cracked open
GV 44 (New Well) |  | 41.2 | 38.5 | 1.6 | 18.7 | 10 | 9 | 999 | -0.26 |  | Off Low gas
GV 45 (New Well) |  | 46.1 | 37.5 | 1.1 | 15.3 | 4 | 7 | 999 | -7.06 |  | Cracked Open
GV 46 (New Well) |  | 51.2 | 38.4 | 0.3 | 10.1 | 6 | 7 | 999 | -27.12 |  | Open Full
GV 47 (New Well) |  | 46.5 | 36.5 | 1 | 16 | 8 | 10 | 999 | -6.99 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 9 | 8 | 999 | -27.41 |  | Open Full
GV 49 (New Well) |  | 47.8 | 37.4 | 1.1 | 13.7 | 6 | 6 | 999 | -6.59 |  | Cracked open
LC1B |  | 36.8 | 32.9 | 1.4 | 28.9 | 6 | 9 | 999 | -1.1 |  | OFF
LC2R? |  | 51.3 | 37.4 | 0.2 | 11.1 | 8 | 10 | 999 | -27.14 |  | Open Full
GV 2.1 |  | 52.4 | 38.5 | 0.3 | 8.8 | 10 | 7 | 999 | -27.59 |  | Open Full
GV 2.2+ LC2B MAN |  | 47.5 | 37.4 | 1.1 | 14 | 6 | 7 | 999 | -7.65 |  | Cracked Open at Manifold
GV 2.2 |  | 48 | 37.7 | 0.9 | 13.4 | 8 | 9 | 999 | -7.99 |  | Cracked Open
LC2B |  | 46.9 | 36.8 | 1.3 | 15 | 5 | 5 | 999 | -7.12 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.5 | 37 | 1 | 14.5 | 5 | 7 | 999 | -11.59 |  | Left Open Half Way
LC3.1 |  | 47.5 | 37 | 1 | 14.5 | 5 | 7 | 999 | -11.59 |  | Left open half way
LC3 |  | 41.9 | 34.5 | 2.5 | 21.1 | 3 | 6 | 999 | -0.21 |  | OFF
LC4B |  | 46 | 36.2 | 1 | 16.8 | 8 | 5 | 999 | -6.56 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.5 | 37 | 0.6 | 13.9 | 7 | 8 | 999 | -27.56 |  | Open Full
R1 |  | 47.2 | 38 | 1.1 | 13.7 | 6 | 6 | 999 | -11.24 |  | Cracked Open
R1B |  | 50.3 | 36.9 | 0.5 | 12.3 | 8 | 10 | 999 | -27.88 |  | Open Full
R2B |  | 50.1 | 37 | 0.2 | 12.7 | 5 | 8 | 999 | -27.45 |  | Open Full
R4B |  | 41.9 | 36.5 | 3.2 | 18.4 | 7 | 10 | 999 | -0.25 |  | Left closed
R6B |  | 51.6 | 37.5 | 0.3 | 10.6 | 5 | 6 | 999 | -27.54 |  | Open Full
LC5 |  | 47.9 | 35.1 | 2.5 | 14.5 | 7 | 10 | 999 | -0.21 |  | Left Off ( Gas drops quick)
LC6 |  | 48.2 | 36 | 3 | 12.8 | 5 | 6 | 999 | -0.18 |  | Left Off ( Gas drops quick)
LC6B |  | 50.2 | 36.2 | 0.5 | 13.1 | 4 | 6 | 999 | -27.89 |  | Open Full
PW1 |  | 2.9 | 0.8 | 11.5 | 84.8 | 6 | 5 | 999 | -0.75 |  | Left Off
PW2 |  | 34.5 | 19.9 | 2.6 | 43 | 10 | 5 | 999 | -0.52 |  | Left Off
PW3 |  | 36.1 | 20.1 | 3.5 | 40.3 | 6 | 7 | 999 | 0.41 |  | Left Off
PW4 |  | 46.5 | 33.6 | 1.1 | 18.8 | 6 | 6 | 999 | -5.59 |  | Cracked Open
PW5 |  | 35.4 | 29.9 | 1.5 | 33.2 | 7 | 4 | 999 | -0.21 |  | Left Off
PW6 |  | 36.9 | 22.4 | 2.7 | 38 | 8 | 6 | 999 | -0.25 |  | Left Off
Flare | 15:00 | 54.3 | 38.1 | 0.3 | 7.3 | 5 | 7 | 999 | 175 |  | Engine running 400KW
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## April 2017
Date | 2017-04-06
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 14 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/09//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 998 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.2 | 1.5 | 20 | 78.3 | 0 | 0 | 998 | -0.57 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 998 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 998 | 0.59 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 998 | 0.77 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 998 | 0.9 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 28.5 | 1.3 | 19.9 | 50.3 | 0 | 0 | 998 | 0.67 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.2 | 1.5 | 20 | 50.3 | 0 | 0 | 998 | 0.69 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 998 | 0.74 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 998 | -0.56 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 998 | 0.41 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 3.3 | 20 | 76.7 | 0 | 0 | 998 | -0.87 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 998 | 0.37 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 998 | 0.52 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.9 | 19.2 | 77.9 | 0 | 0 | 998 | 1.19 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 2.6 | 19.9 | 77.2 | 0 | 0 | 998 | 0.91 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.4 | 2.5 | 20 | 77.1 | 0 | 0 | 998 | 0.67 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 3 | 19.8 | 77.2 | 0 | 0 | 998 | 0.83 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.2 | 1.7 | 19.6 | 78.5 | 0 | 0 | 998 | 0.46 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.4 | 2.6 | 19.7 | 77.3 | 0 | 0 | 998 | 0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.8 | 19.8 | 77.4 | 0 | 0 | 998 | 0.93 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 998 | -0.67 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 998 | 0.63 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-04-13
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/09//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1002 | 0.69 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.3 | 1.4 | 19.9 | 78.4 | 0 | 0 | 1002 | -0.55 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:53 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1002 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:55 | 0 | 0.4 | 19.8 | 79.8 | 0 | 0 | 1002 | 0.54 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1002 | 0.74 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 2 | 20 | 78 | 0 | 0 | 1002 | 0.89 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 28.6 | 1.5 | 19.9 | 50 | 0 | 0 | 1002 | 0.6 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 28.4 | 1.9 | 19.5 | 50.2 | 0 | 0 | 1002 | 0.71 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1002 | 0.89 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1002 | -0.63 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1002 | 0.46 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 3.5 | 19.6 | 76.9 | 0 | 0 | 1002 | -0.78 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 1002 | 0.4 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1002 | 0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 3 | 19.5 | 77.5 | 0 | 0 | 1002 | 1.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.2 | 2.4 | 20 | 77.4 | 0 | 0 | 1002 | 0.84 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.2 | 2.6 | 20.1 | 77.1 | 0 | 0 | 1002 | 0.6 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2.8 | 19.9 | 77.3 | 0 | 0 | 1002 | 0.8 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.3 | 1.9 | 19.7 | 78.1 | 0 | 0 | 1002 | 0.53 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.2 | 2.4 | 19.8 | 77.6 | 0 | 0 | 1002 | 0.67 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1002 | 0.89 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 1002 | -0.66 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 2.4 | 19.5 | 78.1 | 0 | 0 | 1002 | 0.74 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-04-20
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 14 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/09//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.2 | 1.2 | 19.5 | 79.1 | 0 | 0 | 999 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:29 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.58 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 999 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 999 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 1.8 | 19.8 | 78.4 | 0 | 0 | 999 | 0.84 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 28.4 | 1.6 | 19.9 | 50.1 | 0 | 0 | 999 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:46 | 28 | 1.8 | 19.8 | 50.4 | 0 | 0 | 999 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 999 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 999 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:12 | 0 | 3.2 | 19.7 | 77.1 | 0 | 0 | 999 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 999 | 0.41 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 999 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 999 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.3 | 2.6 | 19.9 | 77.2 | 0 | 0 | 999 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.1 | 2.2 | 19.8 | 77.9 | 0 | 0 | 999 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 999 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.4 | 1.5 | 19.6 | 78.5 | 0 | 0 | 999 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.3 | 2.2 | 19.5 | 78 | 0 | 0 | 999 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 2.9 | 19.7 | 77.4 | 0 | 0 | 999 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 0.4 | 19.6 | 80 | 0 | 0 | 999 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 999 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-04-27
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/09//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:52 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1006 | 0.61 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:57 | 0.3 | 1.3 | 19.6 | 78.8 | 0 | 0 | 1006 | -0.51 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:00 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1006 | 0.41 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:02 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1006 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:04 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1006 | 0.62 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:08 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1006 | 0.62 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:11 | 28.6 | 1.5 | 20 | 49.9 | 0 | 0 | 1006 | 0.55 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:16 | 28.2 | 1.7 | 19.5 | 50.6 | 0 | 0 | 1006 | 0.63 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:22 | 0 | 1.6 | 19.7 | 78.7 | 0 | 0 | 1006 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:34 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1006 | -0.49 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:38 | 0 | 2.7 | 19.4 | 77.9 | 0 | 0 | 1006 | 0.3 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:42 | 0 | 3.5 | 19.7 | 76.8 | 0 | 0 | 1006 | -0.71 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:45 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 1006 | 0.4 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:48 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 1006 | 0.44 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:51 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1006 | 0.81 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:58 | 0.2 | 2.8 | 20 | 77 | 0 | 0 | 1006 | 0.5 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:24 | 0.3 | 2.3 | 19.9 | 77.5 | 0 | 0 | 1006 | -0.53 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:28 | 0 | 2.6 | 20.1 | 77.3 | 0 | 0 | 1006 | 0.5 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:31 | 0.2 | 1.4 | 19.8 | 78.6 | 0 | 0 | 1006 | 0.59 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:26 | 0.2 | 2.4 | 19.4 | 78 | 0 | 0 | 1006 | 0.44 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:41 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 1006 | 0.78 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:44 | 0 | 0.5 | 19.7 | 79.8 | 0 | 0 | 1006 | -0.78 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:48 | 0 | 2.7 | 19.9 | 77.4 | 0 | 0 | 1006 | 0.41 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date |  | 2017-04-17
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 14 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-03-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 11:10 | 53.6 | 37.5 | 0.3 | 8.6 | 9 | 6 | 1006 | 180 |  | Flare On 400 KWH
GV1 |  | 34.8 | 26.9 | 1.6 | 36.7 | 4 | 3 | 1006 | -0.22 |  | OFF
GV3 |  | 53.7 | 36.9 | 0.1 | 9.3 | 11 | 8 | 1006 | -26.87 |  | Open Full
GV4 |  | 46.5 | 37.1 | 1.1 | 15.3 | 8 | 5 | 1006 | -10.89 | -5.24 | Reg closed to cracked.
GV6 |  | 46 | 36 | 1.2 | 16.8 | 6 | 6 | 1006 | -6.24 |  | Cracked Open
GV7 |  | 36.5 | 35.4 | 2.6 | 25.5 | 5 | 9 | 1006 | -0.28 |  | Off Low Gas high o2
GV8 |  | 33.1 | 33.9 | 2.8 | 30.2 | 8 | 7 | 1006 | -0.39 |  | Off Low Gas high o3
GV9 |  | 52.6 | 37.2 | 0.1 | 10.1 | 9 | 9 | 1006 | -26.41 |  | Open Full
GV10 |  | 39.2 | 36.5 | 1.5 | 22.8 | 9 | 10 | 1006 | -0.01 |  | Off
GV11 |  | 46.2 | 34.2 | 1.2 | 18.4 | 9 | 11 | 1006 | -11.25 | -4.58 | Reg closed to cracked.
GV12+R3 Manifold |  | 52 | 37.1 | 0.3 | 10.6 | 5 | 6 | 1006 | -26.84 |  | Open Full
GV12 |  | 52.4 | 37.4 | 0.3 | 9.9 | 6 | 8 | 1006 | -26.89 |  | Open Full
R3 |  | 51.6 | 36.6 | 0.4 | 11.4 | 5 | 6 | 1006 | -26.62 |  | Open Full
GV13 |  | 2.9 | 4.1 | 19.2 | 73.8 | 2 | 2 | 1006 | -0.23 |  | Left Closed
GV14 |  | 51.4 | 37.4 | 0.3 | 10.9 | 6 | 8 | 1006 | -26.99 |  | Open Full
GV15 |  | 50.3 | 37.2 | 0.4 | 12.1 | 3 | 10 | 1006 | -26.74 |  | Open Full
GV16 |  | 49.6 | 37 | 0.6 | 12.8 | 10 | 6 | 1006 | -9.45 | -26.38 | Reg opened full
GV17+LC4 Manifold |  | 45.6 | 36 | 2.6 | 15.8 | 7 | 5 | 1006 | -0.09 |  | Off at Manifold Gas drops quick.
GV17 |  | 45 | 36.4 | 2.2 | 16.4 | 8 | 6 | 1006 | -0.11 |  | Open Full at Well
LC4 |  | 46.2 | 35.7 | 3.1 | 15 | 6 | 4 | 1006 | -0.05 |  | Open Full at well
GV18 |  | 51.9 | 37.2 | 0.5 | 10.4 | 8 | 5 | 1006 | -26.74 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.8 | 36.9 | 1.4 | 14.9 | 10 | 6 | 1006 | -0.41 |  | Off gas drops off quick.
GV23 |  | 51.6 | 37.4 | 0.4 | 10.6 | 4 | 5 | 1006 | -26.89 |  | Open Full
GV24 |  | 51.9 | 36.9 | 0.4 | 10.8 | 8 | 9 | 1006 | -26.57 |  | Open Full
GV25 |  | 40.8 | 36.8 | 1.9 | 20.5 | 5 | 6 | 1006 | -0.32 |  | Left Closed
GV26 + 27 Manifold |  | 52.4 | 36.8 | 0.4 | 10.4 | 8 | 6 | 1006 | -26.54 |  | Open Full
GV28+ 29 Manifold |  | 52 | 37.9 | 0.5 | 9.6 | 11 | 7 | 1006 | -26.71 |  | Open Full
GV26 |  | 53 | 36.4 | 0.3 | 10.3 | 6 | 4 | 1006 | -26.74 |  | Open Full
GV27 |  | 51.9 | 37.5 | 0.5 | 10.1 | 9 | 7 | 1006 | -26.36 |  | Open Full
GV28 |  | 52.5 | 37.7 | 0.5 | 9.3 | 10 | 8 | 1006 | -26.79 |  | Open Full
GV29 |  | 51.6 | 38.5 | 0.6 | 9.3 | 12 | 6 | 1006 | -26.62 |  | Open Full
GVA |  | 36.8 | 30.6 | 4.2 | 28.4 | 6 | 5 | 1006 | 0 |  | Off Low gas
B+C Manifold |  | 52 | 37.9 | 0.4 | 9.7 | 7 | 4 | 1006 | -26.58 |  | Open Full
GV B |  | 52.6 | 36.9 | 0.4 | 10.1 | 5 | 6 | 1006 | -26.59 |  | Open Full
GV C |  | 50.6 | 38 | 0.3 | 11.1 | 6 | 4 | 1006 | -26.41 |  | Open Full
GV30 |  | 46.6 | 35.9 | 1.2 | 16.3 | 11 | 1 | 1006 | -7.12 |  | Left Cracked
GV31 |  | 45.8 | 36.1 | 1.1 | 17 | 10 | 10 | 1006 | -6.89 |  | Cracked Open
GV32 |  | 46 | 36.8 | 1.1 | 16.1 | 9 | 9 | 1006 | -6.47 |  | Cracked Open
GV33 |  | 46.4 | 36.5 | 1 | 16.1 | 7 | 6 | 1006 | -6.83 |  | Cracked Open
GV34 |  | 46.5 | 36.9 | 1.1 | 15.5 | 8 | 1 | 1006 | -6.98 |  | Cracked Open
GV 35 (New Well) |  | 25.4 | 26.9 | 1.5 | 46.2 | 4 | 9 | 1006 | -0.74 |  | Left Closed
GV 36 (New Well) |  | 27.5 | 26.8 | 4.9 | 40.8 | 10 | 6 | 1006 | 0 |  | OFF low gas.
GV 37 (New Well) |  | 54 | 36 | 0.6 | 9.4 | 9 | 8 | 1006 | -26.7 |  | Left open Full
GV 38 (New Well) |  | 46.8 | 35.7 | 1.1 | 16.4 | 8 | 10 | 1006 | -7 |  | Cracked Open
GV 39 (New Well) |  | 46.8 | 36 | 1.2 | 16 | 6 | 4 | 1006 | -6.87 |  | Cracked Open
GV 40 (New Well) |  | 46.2 | 35.8 | 1.1 | 16.9 | 10 | 9 | 1006 | -6.49 |  | Cracked Open
GV 41 (New Well) |  | 45.9 | 36 | 1.1 | 17 | 12 | 6 | 1006 | -6.93 |  | Cracked Open
GV 42 (New Well) |  | 40.5 | 36.9 | 1.6 | 21 | 5 | 8 | 1006 | -0.23 |  | Off Low Gas
GV 43 (New Well) |  | 46.8 | 36.9 | 1.1 | 15.2 | 2 | 7 | 1006 | -6.84 |  | Cracked open
GV 44 (New Well) |  | 42 | 38.2 | 1.7 | 18.1 | 9 | 9 | 1006 | -0.32 |  | Off Low gas
GV 45 (New Well) |  | 46.3 | 36.5 | 1.2 | 16 | 7 | 6 | 1006 | -6.87 |  | Cracked Open
GV 46 (New Well) |  | 50.8 | 37.8 | 0.4 | 11 | 4 | 10 | 1006 | -26.32 |  | Open Full
GV 47 (New Well) |  | 46.1 | 36.1 | 1.1 | 16.7 | 9 | 4 | 1006 | -7.14 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 8 | 6 | 1006 | -26.6 |  | Open Full
GV 49 (New Well) |  | 47.1 | 36.8 | 1.2 | 14.9 | 5 | 9 | 1006 | -7.22 |  | Cracked open
LC1B |  | 37.5 | 33.5 | 1.6 | 27.4 | 6 | 10 | 1006 | -1.1 |  | OFF
LC2R? |  | 51.8 | 36.9 | 0.3 | 11 | 10 | 6 | 1006 | -26.32 |  | Open Full
GV 2.1 |  | 50.9 | 38 | 0.2 | 10.9 | 9 | 9 | 1006 | -26.57 |  | Open Full
GV 2.2+ LC2B MAN |  | 47.8 | 37 | 1.1 | 14.1 | 4 | 9 | 1006 | -6.99 |  | Cracked Open at Manifold
GV 2.2 |  | 48.2 | 37.4 | 0.8 | 13.6 | 6 | 10 | 1006 | -6.57 |  | Cracked Open
LC2B |  | 47 | 36.5 | 1.2 | 15.3 | 2 | 7 | 1006 | -7.06 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.1 | 37.1 | 1 | 14.8 | 6 | 8 | 1006 | -10.58 |  | Left Open Half Way
LC3.1 |  | 47.1 | 37.1 | 1 | 14.8 | 6 | 8 | 1006 | -10.58 |  | Left open half way
LC3 |  | 42.2 | 34.2 | 2.2 | 21.4 | 4 | 6 | 1006 | -0.19 |  | OFF
LC4B |  | 46.2 | 36.5 | 1.1 | 16.2 | 10 | 2 | 1006 | -6.85 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.9 | 37.4 | 0.7 | 13 | 9 | 6 | 1006 | -26.74 |  | Open Full
R1 |  | 47.8 | 37.9 | 1 | 13.3 | 5 | 5 | 1006 | -10.99 |  | Cracked Open
R1B |  | 50 | 36.5 | 0.4 | 13.1 | 10 | 9 | 1006 | -27.01 |  | Open Full
R2B |  | 50.4 | 36.5 | 0.3 | 12.8 | 6 | 9 | 1006 | -26.47 |  | Open Full
R4B |  | 42.7 | 36.8 | 3.5 | 17 | 8 | 10 | 1006 | -0.26 |  | Left closed
R6B |  | 51.9 | 37.2 | 0.4 | 10.5 | 6 | 9 | 1006 | -26.99 |  | Open Full
LC5 |  | 47 | 32.7 | 2.6 | 17.7 | 10 | 8 | 1006 | -0.26 |  | Left Off ( Gas drops quick)
LC6 |  | 48.9 | 35.5 | 3.2 | 12.4 | 8 | 12 | 1006 | -0.19 |  | Left Off ( Gas drops quick)
LC6B |  | 50.9 | 36.5 | 0.6 | 12 | 9 | 6 | 1006 | -26.54 |  | Open Full
PW1 |  | 2.8 | 1.2 | 10.6 | 85.4 | 14 | 7 | 1006 | -0.75 |  | Left Off
PW2 |  | 33.6 | 20.1 | 2.9 | 43.4 | 12 | 9 | 1006 | -0.41 |  | Left Off
PW3 |  | 36.4 | 19.9 | 3.6 | 40.1 | 11 | 10 | 1006 | -0.26 |  | Left Off
PW4 |  | 47.5 | 34.2 | 1.2 | 17.1 | 6 | 11 | 1006 | -6.54 |  | Cracked Open
PW5 |  | 36.2 | 28.7 | 1.4 | 33.7 | 9 | 7 | 1006 | -0.34 |  | Left Off
PW6 |  | 35.1 | 23.6 | 2.5 | 38.8 | 8 | 9 | 1006 | -0.29 |  | Left Off
Flare | 14:35 | 53.7 | 37.6 | 0.3 | 8.4 | 9 | 6 | 1006 | 180 |  | Engine running 400KW
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## May 2017
Date | 2017-05-04
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:15 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 997 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:20 | 0.2 | 1.1 | 19.6 | 79.1 | 0 | 0 | 997 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:22 | 0 | 1.1 | 19.4 | 79.5 | 0 | 0 | 997 | 0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:24 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 997 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:27 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 997 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:31 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:34 | 28.5 | 1.4 | 19.8 | 50.3 | 0 | 0 | 997 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:40 | 28 | 1.6 | 19.6 | 50.8 | 0 | 0 | 997 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:45 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 997 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:57 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:01 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 997 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:05 | 0 | 3.2 | 19.8 | 77 | 0 | 0 | 997 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:08 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 997 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:11 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 997 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:14 | 0 | 1.9 | 19.7 | 78.4 | 0 | 0 | 997 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:21 | 0.2 | 2.4 | 19.6 | 77.8 | 0 | 0 | 997 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:47 | 0.1 | 2.1 | 19.8 | 78 | 0 | 0 | 997 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:51 | 0 | 2.5 | 19.3 | 78.2 | 0 | 0 | 997 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:54 | 0.3 | 1.4 | 19.5 | 78.8 | 0 | 0 | 997 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:59 | 0.1 | 2.6 | 19.8 | 77.5 | 0 | 0 | 997 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:04 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 997 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:07 | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 997 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:11 | 0 | 2.5 | 19 | 78.5 | 0 | 0 | 997 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-05-11
Weather: | Breezy
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:05 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1000 | 0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:10 | 0.3 | 0.8 | 19.8 | 79.1 | 0 | 0 | 1000 | -0.66 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:12 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1000 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:14 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1000 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:17 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1000 | 0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:21 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1000 | 0.45 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:24 | 28.2 | 1.5 | 19.6 | 50.7 | 0 | 0 | 1000 | -0.26 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:30 | 28.4 | 1.9 | 19.5 | 50.2 | 0 | 0 | 1000 | 0.55 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:35 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1000 | 0.77 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:47 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1000 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:51 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 1000 | 0.29 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:55 | 0 | 3.1 | 19.4 | 77.5 | 0 | 0 | 1000 | -0.67 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:58 | 0 | 1.7 | 19.3 | 79 | 0 | 0 | 1000 | 0.33 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:01 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1000 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:04 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1000 | 0.68 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:11 | 0.3 | 2.6 | 20 | 77.1 | 0 | 0 | 1000 | 0.47 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:37 | 0.2 | 2.2 | 20 | 77.6 | 0 | 0 | 1000 | -0.45 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:41 | 0 | 2.4 | 19.5 | 78.1 | 0 | 0 | 1000 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:44 | 0.1 | 1.6 | 19.8 | 78.5 | 0 | 0 | 1000 | 0.03 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:49 | 0.2 | 2.1 | 20 | 77.7 | 0 | 0 | 1000 | 0.18 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:54 | 0 | 2.2 | 19.6 | 78.2 | 0 | 0 | 1000 | 0.43 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:57 | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 1000 | -0.5 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:01 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1000 | 0.42 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-05-18
Weather: | Breezy
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.3 | 19.9 | 78.8 | 0 | 0 | 997 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.2 | 0.7 | 20 | 79.1 | 0 | 0 | 997 | -0.57 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 997 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 997 | 0.59 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 997 | 0.77 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 997 | 0.9 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 29 | 1.4 | 19.8 | 49.8 | 0 | 0 | 997 | 0.67 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.9 | 1.8 | 19.6 | 49.7 | 0 | 0 | 997 | 0.69 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 997 | 0.74 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 997 | -0.56 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 997 | 0.41 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 3 | 19.7 | 77.3 | 0 | 0 | 997 | -0.87 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 997 | 0.37 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 997 | 0.52 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 997 | 1.19 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.2 | 2.9 | 19.8 | 77.1 | 0 | 0 | 997 | 0.91 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.3 | 2.6 | 19.3 | 77.8 | 0 | 0 | 997 | 0.67 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 997 | 0.83 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.2 | 1.4 | 19.7 | 78.7 | 0 | 0 | 997 | 0.46 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.3 | 2 | 19.8 | 77.9 | 0 | 0 | 997 | 0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.93 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 997 | -0.67 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 997 | 0.63 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-05-25
Weather: | Breezy
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1005 | 0.69 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.3 | 0.8 | 19.9 | 79 | 0 | 0 | 1005 | -0.55 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:53 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 1005 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:55 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1005 | 0.54 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1005 | 0.74 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 2 | 20 | 78 | 0 | 0 | 1005 | 0.89 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 29.1 | 1.6 | 19.6 | 49.7 | 0 | 0 | 1005 | 0.6 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 28.6 | 1.9 | 19.5 | 50 | 0 | 0 | 1005 | 0.71 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1005 | 0.89 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1005 | -0.63 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 1005 | 0.46 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 3.6 | 19.5 | 76.9 | 0 | 0 | 1005 | -0.78 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1005 | 0.4 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1005 | 0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1005 | 1.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.3 | 2.5 | 19.6 | 77.6 | 0 | 0 | 1005 | 0.84 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.2 | 2.4 | 19.4 | 78 | 0 | 0 | 1005 | 0.6 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 1005 | 0.8 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.3 | 1.6 | 19.3 | 78.8 | 0 | 0 | 1005 | 0.53 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.2 | 2.1 | 19.5 | 78.2 | 0 | 0 | 1005 | 0.67 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 1005 | 0.89 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 1005 | -0.66 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1005 | 0.74 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-05-15
Weather: |  | Dry
Wind conditions: |  | Breezy
Air Temperature: |  | 12 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 11:00 | 52.1 | 38.9 | 0.4 | 8.6 | 6 | 3 | 999 | 175 |  | Engine running 390 KW
GV1 |  | 35.6 | 27.5 | 1.7 | 35.2 | 6 | 2 | 999 | -0.23 |  | OFF
GV3 |  | 54.6 | 37 | 0.2 | 8.2 | 5 | 5 | 999 | -27.54 |  | Open Full
GV4 |  | 46.4 | 36.9 | 1 | 15.7 | 8 | 2 | 999 | -4.99 | -5.55 | Left Cracked
GV6 |  | 46.2 | 35.8 | 1.1 | 16.9 | 6 | 4 | 999 | -5.23 |  | Cracked Open
GV7 |  | 37.5 | 31.8 | 2.5 | 28.2 | 1 | 1 | 999 | -0.01 |  | Off Low Gas high o2
GV8 |  | 34.5 | 34.5 | 2.4 | 28.6 | 2 | 6 | 999 | -0.42 |  | Off Low Gas high o3
GV9 |  | 52.1 | 37 | 0.3 | 10.6 | 4 | 8 | 999 | -27.58 |  | Open Full
GV10 |  | 38.7 | 36.2 | 1.4 | 23.7 | 10 | 11 | 999 | -0.08 |  | Off
GV11 |  | 47 | 35.6 | 1.3 | 16.1 | 6 | 5 | 999 | -4.99 | -12.57 | Reg Opened Half Way
GV12+R3 Manifold |  | 52.3 | 37.2 | 0.4 | 10.1 | 7 | 6 | 999 | -27.88 |  | Open Full
GV12 |  | 52.8 | 37.5 | 0.3 | 9.4 | 5 | 9 | 999 | -27.01 |  | Open Full
R3 |  | 51.3 | 36.4 | 0.4 | 11.9 | 9 | 4 | 999 | -27.99 |  | Open Full
GV13 |  | 2.8 | 4.6 | 19.5 | 73.1 | 6 | 4 | 999 | -0.21 |  | Left Closed
GV14 |  | 51.6 | 36.8 | 0.2 | 11.4 | 3 | 5 | 999 | -27.55 |  | Open Full
GV15 |  | 50.4 | 36.5 | 0.3 | 12.8 | 5 | 2 | 999 | -27.34 |  | Open Full
GV16 |  | 48.7 | 36.9 | 0.5 | 13.9 | 2 | 2 | 999 | -27.89 |  | Left Open Full
GV17+LC4 Manifold |  | 45.2 | 36.2 | 2.5 | 16.1 | 5 | 5 | 999 | -0.11 |  | Off at Manifold Gas drops quick.
GV17 |  | 45 | 36.5 | 2.3 | 16.2 | 2 | 4 | 999 | -0.18 |  | Open Full at Well
LC4 |  | 46 | 35.6 | 3 | 15.4 | 8 | 7 | 999 | -0.02 |  | Open Full at well
GV18 |  | 50.8 | 36.5 | 0.6 | 12.1 | 6 | 7 | 999 | -27.19 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.2 | 36.4 | 1.2 | 16.2 | 10 | 6 | 999 | -0.52 |  | Off gas drops off quick.
GV23 |  | 51.1 | 36.7 | 0.3 | 11.9 | 4 | 8 | 999 | -27.41 |  | Open Full
GV24 |  | 50.3 | 36.5 | 0.2 | 13 | 8 | 9 | 999 | -27.23 |  | Open Full
GV25 |  | 41.2 | 36.5 | 1.6 | 20.7 | 5 | 6 | 999 | -0.35 |  | Left Closed
GV26 + 27 Manifold |  | 51.8 | 37.8 | 0.3 | 10.1 | 8 | 5 | 999 | -27.52 |  | Open Full
GV28+ 29 Manifold |  | 52.4 | 36.9 | 0.3 | 10.4 | 11 | 7 | 999 | -27.53 |  | Open Full
GV26 |  | 52.6 | 36.6 | 0.3 | 10.5 | 6 | 8 | 999 | -27.69 |  | Open Full
GV27 |  | 51.5 | 38 | 0.4 | 10.1 | 9 | 3 | 999 | -27.38 |  | Open Full
GV28 |  | 52.8 | 36.5 | 0.2 | 10.5 | 10 | 6 | 999 | -27.6 |  | Open Full
GV29 |  | 51.3 | 37.5 | 0.5 | 10.7 | 12 | 8 | 999 | -27.52 |  | Open Full
GVA |  | 37.5 | 31.5 | 3.9 | 27.1 | 6 | 9 | 999 | 0 |  | Off Low gas
B+C Manifold |  | 51.8 | 36.5 | 0.3 | 11.4 | 7 | 6 | 999 | -27.62 |  | Open Full
GV B |  | 52.4 | 36.9 | 0.4 | 10.3 | 5 | 9 | 999 | -27.88 |  | Open Full
GV C |  | 50 | 36 | 0.3 | 13.7 | 8 | 8 | 999 | -27.31 |  | Open Full
GV30 |  | 46 | 36.2 | 1.1 | 16.7 | 11 | 6 | 999 | -7.99 | -5.23 | Left Cracked
GV31 |  | 46 | 36.7 | 1 | 16.3 | 10 | 14 | 999 | -8.23 | -5.88 | Cracked Open
GV32 |  | 46.2 | 36.6 | 1.1 | 16.1 | 9 | 9 | 999 | -6.21 |  | Cracked Open
GV33 |  | 45.9 | 35.5 | 1.1 | 17.5 | 7 | 8 | 999 | -6 |  | Cracked Open
GV34 |  | 46.7 | 36 | 1 | 16.3 | 8 | 7 | 999 | -5.28 |  | Cracked Open
GV 35 (New Well) |  | 22.6 | 28.7 | 1.6 | 47.1 | 4 | 9 | 999 | -0.71 |  | Left Closed
GV 36 (New Well) |  | 28.9 | 27.8 | 4.6 | 38.7 | 10 | 8 | 999 | 0 |  | OFF low gas.
GV 37 (New Well) |  | 46.3 | 36 | 0.8 | 16.9 | 9 | 11 | 999 | -27.69 |  | Left open Full
GV 38 (New Well) |  | 45.9 | 35.6 | 1 | 17.5 | 8 | 12 | 999 | -7.56 | -5.47 | Cracked Open
GV 39 (New Well) |  | 45.6 | 36.9 | 1.1 | 16.4 | 6 | 5 | 999 | -6.02 |  | Cracked Open
GV 40 (New Well) |  | 45.8 | 36.8 | 1.1 | 16.3 | 10 | 3 | 999 | -6.23 |  | Cracked Open
GV 41 (New Well) |  | 46 | 37 | 1.2 | 15.8 | 12 | 6 | 999 | -5.57 |  | Cracked Open
GV 42 (New Well) |  | 39.9 | 30 | 1.9 | 28.2 | 5 | 6 | 999 | -0.21 |  | Off Low Gas
GV 43 (New Well) |  | 46.2 | 36.2 | 1.1 | 16.5 | 2 | 1 | 999 | -7.44 | -6.21 | Cracked open
GV 44 (New Well) |  | 40 | 37.4 | 1.2 | 21.4 | 9 | 5 | 999 | -0.25 |  | Off Low gas
GV 45 (New Well) |  | 46.1 | 35.9 | 1.1 | 16.9 | 7 | 6 | 999 | -5.87 |  | Cracked Open
GV 46 (New Well) |  | 49.9 | 36.8 | 0.3 | 13 | 4 | 8 | 999 | -27.77 |  | Open Full
GV 47 (New Well) |  | 47.8 | 36.5 | 1.2 | 14.5 | 9 | 7 | 999 | -5.89 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 8 | 10 | 999 | -27.23 |  | Open Full
GV 49 (New Well) |  | 46.9 | 36.5 | 1.1 | 15.5 | 5 | 9 | 999 | -8.98 | -6.32 | Cracked open
LC1B |  | 36.5 | 31.2 | 1.8 | 30.5 | 7 | 8 | 999 | -1.21 |  | OFF
LC2R? |  | 51.2 | 36.5 | 0.2 | 12.1 | 8 | 9 | 999 | -27.55 |  | Open Full
GV 2.1 |  | 50.8 | 37.2 | 0.4 | 11.6 | 9 | 6 | 999 | -27.4 |  | Open Full
GV 2.2+ LC2B MAN |  | 48 | 36.5 | 1 | 14.5 | 6 | 10 | 999 | -7 |  | Cracked Open at Manifold
GV 2.2 |  | 48.6 | 37.5 | 0.7 | 13.2 | 8 | 11 | 999 | -6.62 |  | Cracked Open
LC2B |  | 47.2 | 36.4 | 1.1 | 15.3 | 4 | 10 | 999 | -7.11 |  | Cracked Open
GV / LC3.1 + LC3 MAN |  | 47.5 | 35.2 | 1 | 16.3 | 8 | 2 | 999 | -11.21 |  | Left Open Half Way
LC3.1 |  | 47.5 | 35.2 | 1 | 16.3 | 8 | 2 | 999 | -11.21 |  | Left open half way
LC3 |  | 43.8 | 33.5 | 2.8 | 19.9 | 12 | 8 | 999 | -0.08 |  | OFF
LC4B |  | 47.8 | 35.8 | 1.2 | 15.2 | 14 | 6 | 999 | -6.05 |  | Left Cracked Open
R1 + R1B Manifold |  | 49 | 36.9 | 0.6 | 13.5 | 17 | 7 | 999 | -27.19 |  | Open Full
R1 |  | 47.8 | 37.4 | 0.9 | 13.9 | 8 | 5 | 999 | -10.2 |  | Cracked Open
R1B |  | 50.1 | 36.4 | 0.4 | 13.1 | 19 | 7 | 999 | -27.88 |  | Open Full
R2B |  | 50.8 | 36.4 | 0.2 | 12.6 | 6 | 8 | 999 | -27.45 |  | Open Full
R4B |  | 41.8 | 35.8 | 3.6 | 18.8 | 9 | 8 | 999 | -0.39 |  | Left closed
R6B |  | 51 | 36.2 | 0.2 | 12.6 | 8 | 4 | 999 | -27.81 |  | Open Full
LC5 |  | 46.9 | 34.9 | 2.2 | 16 | 10 | 6 | 999 | -0.36 |  | Left Off ( Gas drops quick)
LC6 |  | 47.2 | 35.6 | 3.1 | 14.1 | 6 | 5 | 999 | -0.24 |  | Left Off ( Gas drops quick)
LC6B |  | 50.5 | 36.2 | 0.4 | 12.9 | 8 | 1 | 999 | -27.41 |  | Open Full
PW1 |  | 2.4 | 1.6 | 9.9 | 86.1 | 7 | 9 | 999 | -0.82 |  | Left Off
PW2 |  | 32.5 | 19.8 | 2.5 | 45.2 | 9 | 4 | 999 | -0.53 |  | Left Off
PW3 |  | 31.7 | 20 | 3.1 | 45.2 | 12 | 10 | 999 | -0.14 |  | Left Off
PW4 |  | 48 | 33.6 | 1.1 | 17.3 | 16 | 9 | 999 | -6.03 |  | Cracked Open
PW5 |  | 37.8 | 27.5 | 1.6 | 33.1 | 9 | 6 | 999 | -0.45 |  | Left Off
PW6 |  | 36.6 | 22.1 | 2.9 | 38.4 | 8 | 10 | 999 | -0.39 |  | Left Off
Flare | 14:00 | 52.2 | 38.7 | 0.4 | 8.7 | 6 | 3 | 999 | 175 |  | Engine running 390 KW
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## June 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-06-01
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 18 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1003 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.2 | 0.9 | 20 | 78.9 | 0 | 0 | 1003 | 0.32 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:52 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1003 | -0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1003 | 0.28 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1003 | 0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 2.3 | 19 | 78.7 | 0 | 0 | 1003 | -0.65 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 29.4 | 1.6 | 19.2 | 49.8 | 0 | 0 | 1003 | 0.34 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 28.7 | 1.5 | 19.2 | 50.6 | 0 | 0 | 1003 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 1003 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1003 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 1003 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 3.5 | 19.6 | 76.9 | 0 | 0 | 1003 | 0.69 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.6 | 19.3 | 79.1 | 0 | 0 | 1003 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1003 | 0.23 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1003 | -0.42 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.2 | 2.4 | 19.8 | 77.6 | 0 | 0 | 1003 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.3 | 2.5 | 19.9 | 77.3 | 0 | 0 | 1003 | -0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2 | 19.3 | 78.7 | 0 | 0 | 1003 | -0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.2 | 1.9 | 19.8 | 78.1 | 0 | 0 | 1003 | 0.6 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.3 | 2.3 | 20 | 77.4 | 0 | 0 | 1003 | 0.27 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.2 | 19.4 | 78.4 | 0 | 0 | 1003 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.4 | 19.8 | 79.8 | 0 | 0 | 1003 | 0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1003 | -0.58 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-06-08
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.4 | 20.1 | 78.5 | 0 | 0 | 996 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.3 | 0.8 | 19.9 | 79 | 0 | 0 | 996 | 0.49 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.1 | 19.7 | 79.2 | 0 | 0 | 996 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 996 | 0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 996 | 0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 996 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 29.5 | 1.5 | 19.4 | 49.6 | 0 | 0 | 996 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.9 | 1.9 | 19.8 | 49.4 | 0 | 0 | 996 | 0.53 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.2 | 19.3 | 79.5 | 0 | 0 | 996 | 0.24 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 996 | -0.11 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 996 | 0.56 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 3.6 | 19.8 | 76.6 | 0 | 0 | 996 | 0.38 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 996 | 0.14 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 2 | 19.3 | 78.7 | 0 | 0 | 996 | 0.25 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 996 | 0.36 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 2.6 | 19.7 | 77.4 | 0 | 0 | 996 | -0.14 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.2 | 2.4 | 19.4 | 78 | 0 | 0 | 996 | 0.36 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 996 | -0.98 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.4 | 1.5 | 19.9 | 78.2 | 0 | 0 | 996 | 0.75 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.2 | 2.6 | 19.9 | 77.3 | 0 | 0 | 996 | -0.15 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 996 | 0.36 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 996 | -0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 996 | 0.21 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-06-15
Weather: | Dry
Wind conditions: | SW/slight breeze
Air Temperature: | 18 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 15:35 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 1013 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 15:44 | 0.2 | 1.2 | 19.9 | 78.7 | 0 | 0 | 1013 | 0.49 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 15:56 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1013 | 0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 16:04 | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1013 | 0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 16:13 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1013 | 0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 21 | 15:00 | 0.3 | 2.4 | 19.7 | 77.6 | 0 | 0 | 1013 | -0.15 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 15:08 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1013 | 0.36 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 15:16 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1013 | -0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 15:25 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1013 | 0.21 | 1 | 9.9 | 0.5 | 4.95
Engine running at 400KW during investigation.
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-06-22
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1004 | -0.19 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.2 | 1 | 20 | 78.8 | 0 | 0 | 1004 | 0.68 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1004 | 0.35 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1004 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1004 | -0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1004 | 0.35 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 29.6 | 1.6 | 19.5 | 49.3 | 0 | 0 | 1004 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 29 | 1.5 | 19.8 | 49.7 | 0 | 0 | 1004 | 0.24 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1004 | -0.35 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1004 | -0.14 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 1.8 | 19.7 | 78.5 | 0 | 0 | 1004 | 0.38 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 3.5 | 19.9 | 76.6 | 0 | 0 | 1004 | -0.14 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 1004 | 0.65 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 2.5 | 19.5 | 78 | 0 | 0 | 1004 | 0.32 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.3 | 19.2 | 78.5 | 0 | 0 | 1004 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.2 | 1.9 | 19.6 | 78.3 | 0 | 0 | 1004 | 0.78 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.2 | 1.2 | 19.8 | 78.8 | 0 | 0 | 1004 | 0.54 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1004 | -0.16 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.3 | 1.7 | 20 | 78 | 0 | 0 | 1004 | 0.77 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.1 | 2.3 | 19.8 | 77.8 | 0 | 0 | 1004 | 0.36 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.2 | 19.9 | 77.9 | 0 | 0 | 1004 | -0.57 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1004 | 0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.2 | 19.7 | 78.1 | 0 | 0 | 1004 | 0.67 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-06-29
Weather: | Dry
Wind conditions: | Slight Breeze
Air Temperature: | 16 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:28 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.5 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:33 | 0.3 | 1.2 | 19.8 | 78.7 | 0 | 0 | 1002 | 0.71 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:35 | 0 | 1.1 | 19.4 | 79.5 | 0 | 0 | 1002 | 0.65 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:37 | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1002 | 0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:40 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1002 | 0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 9:44 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 1002 | -0.15 | 1 | 10 | 0.5 | 5
BK BH 8 | 9:47 | 29.4 | 1.6 | 19.9 | 49.1 | 0 | 0 | 1002 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 9:53 | 29.2 | 1.3 | 19.7 | 49.8 | 0 | 0 | 1002 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 9:58 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1002 | 0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:10 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1002 | 0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:14 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1002 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:18 | 0 | 3.2 | 19.8 | 77 | 0 | 0 | 1002 | 0.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:21 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.46 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:24 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1002 | -0.14 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:27 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1002 | 0.69 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:34 | 0.3 | 1.6 | 19.3 | 78.8 | 0 | 0 | 1002 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:00 | 0.2 | 1.5 | 19.7 | 78.6 | 0 | 0 | 1002 | -0.47 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:04 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | -0.15 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:07 | 0.4 | 1.9 | 19.5 | 78.2 | 0 | 0 | 1002 | 0.63 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:12 | 0.3 | 2.1 | 19.9 | 77.7 | 0 | 0 | 1002 | -0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:17 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:20 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1002 | 0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:24 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-06-23
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 15 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative |  | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 11:00 | 46.9 | 37.8 | 2.5 | 12.8 | 7 | 4 | 1012 | 170 |  | Engine running 390 KW
GV1 |  | 35.8 | 26.9 | 1.6 | 35.7 | 6 | 5 | 1012 | -0.32 |  | OFF
GV3 |  | 53.9 | 36.5 | 0.3 | 9.3 | 8 | 4 | 1012 | -29.69 |  | Open Full
GV4 |  | 46.9 | 35.8 | 1.1 | 16.2 | 7 | 9 | 1012 | -5.87 |  | Left Cracked
GV6 |  | 46 | 36 | 1 | 17 | 11 | 6 | 1012 | -5.59 |  | Cracked Open
GV7 |  | 38 | 32.8 | 2.3 | 26.9 | 9 | 10 | 1012 | -0.01 |  | Off Low Gas high o2
GV8 |  | 35.2 | 33.6 | 2.2 | 29 | 6 | 3 | 1012 | -0.33 |  | Off Low Gas high o3
GV9 |  | 52.3 | 36.9 | 0.4 | 10.4 | 4 | 5 | 1012 | -29 |  | Open Full
GV10 |  | 39 | 35.9 | 1.6 | 23.5 | 10 | 4 | 1012 | -0.08 |  | Off
GV11 |  | 47.5 | 36 | 1.1 | 15.4 | 8 | 6 | 1012 | -11.25 | -7.54 | Reg Closed to cracked
GV12+R3 Manifold |  | 51.8 | 36.9 | 0.3 | 11 | 7 | 9 | 1012 | -29.41 |  | Open Full
GV12 |  | 52.5 | 37.4 | 0.3 | 9.8 | 5 | 10 | 1012 | -29.4 |  | Open Full
R3 |  | 51.4 | 36.5 | 0.4 | 11.7 | 8 | 5 | 1012 | -29.48 |  | Open Full
GV13 |  | 2.6 | 4.5 | 19.2 | 73.7 | 6 | 1 | 1012 | -0.28 |  | Left Closed
GV14 |  | 51.8 | 36.5 | 0.3 | 11.4 | 5 | 6 | 1012 | -29.14 |  | Open Full
GV15 |  | 51 | 36.9 | 0.5 | 11.6 | 8 | 5 | 1012 | -29.39 |  | Open Full
GV16 |  | 38.6 | 37 | 0.8 | 23.6 | 4 | 3 | 1012 | -29.58 | -0.01 | Reg closed low gas
GV17+LC4 Manifold |  | 46.5 | 37 | 2.6 | 13.9 | 5 | 6 | 1012 | -0.07 |  | Off at Manifold Gas drops quick.
GV17 |  | 45 | 37.5 | 2.4 | 15.1 | 2 | 4 | 1012 | -0.07 |  | Open Full at Well
LC4 |  | 47.2 | 35.9 | 3.1 | 13.8 | 7 | 6 | 1012 | -0.06 |  | Open Full at well
GV18 |  | 51.2 | 37 | 0.8 | 11 | 9 | 5 | 1012 | -29.58 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.2 | 35.6 | 1.74 | 16.46 | 5 | 8 | 1012 | -0.41 |  | Off gas drops off quick.
GV23 |  | 50.2 | 37 | 0.2 | 12.6 | 10 | 6 | 1012 | -29.87 |  | Open Full
GV24 |  | 50.5 | 36.9 | 0.4 | 12.2 | 7 | 5 | 1012 | -29.36 |  | Open Full
GV25 |  | 42.2 | 35.1 | 1.7 | 21 | 6 | 9 | 1012 | -0.38 |  | Left Closed
GV26 + 27 Manifold |  | 51.6 | 37.2 | 0.4 | 10.8 | 7 | 6 | 1012 | -29.87 |  | Open Full
GV28+ 29 Manifold |  | 52 | 37 | 0.3 | 10.7 | 10 | 6 | 1012 | -29.41 |  | Open Full
GV26 |  | 52.3 | 36.9 | 0.3 | 10.5 | 5 | 8 | 1012 | -29.99 |  | Open Full
GV27 |  | 51.4 | 37.2 | 0.5 | 10.9 | 9 | 4 | 1012 | -29.56 |  | Open Full
GV28 |  | 52.5 | 36.5 | 0.3 | 10.7 | 9 | 7 | 1012 | -29.59 |  | Open Full
GV29 |  | 51.4 | 37.4 | 0.4 | 10.8 | 11 | 5 | 1012 | -29.4 |  | Open Full
GVA |  | 36.9 | 28.9 | 3.5 | 30.7 | 5 | 8 | 1012 | 0 |  | Off Low gas
B+C Manifold |  | 50.4 | 36.8 | 0.4 | 12.4 | 7 | 9 | 1012 | -29.54 |  | Open Full
GV B |  | 51.8 | 37 | 0.4 | 10.8 | 5 | 10 | 1012 | -29.58 |  | Open Full
GV C |  | 50.1 | 36.2 | 0.3 | 13.4 | 8 | 8 | 1012 | -29.47 |  | Open Full
GV30 |  | 51.2 | 36.4 | 0.9 | 11.5 | 10 | 7 | 1012 | -7.85 | -11.24 | cracked open
GV31 |  | 49.9 | 37 | 1 | 12.1 | 4 | 10 | 1012 | -7.89 | -10.45 | Cracked Open
GV32 |  | 50.3 | 36.9 | 1 | 11.8 | 8 | 9 | 1012 | -6.55 | -11.78 | Cracked Open
GV33 |  | 49.8 | 35.9 | 1 | 13.3 | 6 | 6 | 1012 | -6.59 | -10.41 | Cracked Open
GV34 |  | 46.2 | 36.5 | 0.9 | 16.4 | 10 | 8 | 1012 | -5 |  | Cracked Open
GV 35 (New Well) |  | 23.4 | 26.9 | 1.4 | 48.3 | 3 | 10 | 1012 | -0.65 |  | Left Closed
GV 36 (New Well) |  | 30.2 | 27.4 | 4.5 | 37.9 | 7 | 6 | 1012 | 0 |  | OFF low gas.
GV 37 (New Well) |  | 41.2 | 36.5 | 1.5 | 20.8 | 4 | 9 | 1012 | -29.54 | -0.01 | Reg closed hign o2 low gas
GV 38 (New Well) |  | 45 | 36.4 | 1 | 17.6 | 10 | 10 | 1012 | -7.21 |  | Cracked Open
GV 39 (New Well) |  | 45.2 | 36.5 | 1 | 17.3 | 8 | 6 | 1012 | -6.32 |  | Cracked Open
GV 40 (New Well) |  | 45.9 | 37 | 1 | 16.1 | 9 | 8 | 1012 | -6.07 |  | Cracked Open
GV 41 (New Well) |  | 46.2 | 36.6 | 1.1 | 16.1 | 6 | 9 | 1012 | -5.74 |  | Cracked Open
GV 42 (New Well) |  | 38.6 | 31.4 | 1.8 | 28.2 | 10 | 7 | 1012 | -0.17 |  | Off Low Gas
GV 43 (New Well) |  | 47 | 36.5 | 1.2 | 15.3 | 6 | 5 | 1012 | -7.06 |  | Cracked open
GV 44 (New Well) |  | 39.8 | 36.9 | 1.4 | 21.9 | 9 | 6 | 1012 | -0.25 |  | Off Low gas
GV 45 (New Well) |  | 46.5 | 36.5 | 1.2 | 15.8 | 6 | 9 | 1012 | -5.99 |  | Cracked Open
GV 46 (New Well) |  | 49.7 | 36.5 | 0.4 | 13.4 | 8 | 10 | 1012 | -29.41 |  | Open Full
GV 47 (New Well) |  | 47.8 | 36.9 | 1.1 | 14.2 | 7 | 4 | 1012 | -6.21 |  | Cracked Opem
GV 48 (New Well) |  | 59.8 | 40 | 0.1 | 0.1 | 7 | 8 | 1012 | -29.43 |  | Open Full
GV 49 (New Well) |  | 42.5 | 36.9 | 2 | 18.6 | 9 | 7 | 1012 | -8.04 | -0.01 | Reg closed hign o2
LC1B |  | 36.9 | 32.5 | 1.7 | 28.9 | 5 | 10 | 1012 | -0.99 |  | OFF
LC2R? |  | 51 | 36.4 | 0.3 | 12.3 | 6 | 6 | 1012 | -29.75 |  | Open Full
GV 2.1 |  | 50.5 | 37.4 | 0.3 | 11.8 | 10 | 8 | 1012 | -29.36 |  | Open Full
GV 2.2+ LC2B MAN |  | 36.9 | 30.4 | 7.5 | 25.2 | 5 | 11 | 1012 | -8.01 | -0.01 | Reg closed Hign o2
GV 2.2 |  | 37.8 | 33.3 | 4.5 | 24.4 | 7 | 11 | 1012 | -7 | -0.01 | Reg closed High o2
LC2B |  | 30.1 | 33.6 | 8.9 | 27.4 | 3 | 10 | 1012 | -8.24 |  | Reg closed hign o2
GV / LC3.1 + LC3 MAN |  | 46.5 | 36 | 1 | 16.5 | 7 | 1 | 1012 | -10.55 |  | Left Open Half Way
LC3.1 |  | 46.5 | 36 | 1 | 16.5 | 7 | 1 | 1012 | -10.55 |  | Left open half way
LC3 |  | 42.5 | 34.9 | 2.5 | 20.1 | 10 | 6 | 1012 | -0.06 |  | OFF
LC4B |  | 47.5 | 36.2 | 1.3 | 15 | 12 | 5 | 1012 | -6.47 |  | Left Cracked Open
R1 + R1B Manifold |  | 48.5 | 36.5 | 0.8 | 14.2 | 10 | 6 | 1012 | -29.55 |  | Open Full
R1 |  | 48 | 37 | 1.2 | 13.8 | 9 | 4 | 1012 | -9.93 |  | Cracked Open
R1B |  | 49.5 | 36.2 | 0.8 | 13.5 | 15 | 8 | 1012 | -29.61 |  | Open Full
R2B |  | 50.5 | 36.1 | 0.3 | 13.1 | 6 | 10 | 1012 | -29.45 |  | Open Full
R4B |  | 42.8 | 36 | 2.7 | 18.5 | 8 | 6 | 1012 | -0.42 |  | Left closed
R6B |  | 50.1 | 36.5 | 0.3 | 13.1 | 5 | 3 | 1012 | -29.54 |  | Open Full
LC5 |  | 45.5 | 33.5 | 2.3 | 18.7 | 10 | 2 | 1012 | -0.21 |  | Left Off ( Gas drops quick)
LC6 |  | 46.2 | 35 | 2.9 | 15.9 | 2 | 4 | 1012 | -0.36 |  | Left Off ( Gas drops quick)
LC6B |  | 50.8 | 36.5 | 0.3 | 12.4 | 6 | 10 | 1012 | -28.99 |  | Open Full
PW1 |  | 2.3 | 1.8 | 9.5 | 86.4 | 3 | 2 | 1012 | -0.41 |  | Left Off
PW2 |  | 33.6 | 20 | 2.6 | 43.8 | 4 | 9 | 1012 | -0.59 |  | Left Off
PW3 |  | 29.8 | 19.9 | 4 | 46.3 | 4 | 8 | 1012 | -0.24 |  | Left Off
PW4 |  | 47.9 | 33.9 | 1.3 | 16.9 | 10 | 6 | 1012 | -6.25 |  | Cracked Open
PW5 |  | 35 | 26.9 | 1.4 | 36.7 | 8 | 3 | 1012 | -0.52 |  | Left Off
PW6 |  | 37.8 | 23.6 | 3 | 35.6 | 9 | 1 | 1012 | -0.49 |  | Left Off
Flare | 14:00 | 50.8 | 38.5 | 0.8 | 9.9 | 7 | 4 | 1012 | 170 |  | Engine running 390 KW o2 dropped CH4 increased. Flow 425m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## July 2017
Date | 2017-07-06
Weather: | Dry
Wind conditions: | Slight Breeze
Air Temperature: | 17 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:15 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1004 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:20 | 0.2 | 1.1 | 19.8 | 78.9 | 0 | 0 | 1004 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:22 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1004 | 0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:24 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1004 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:27 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 1004 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:31 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1004 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:34 | 29.1 | 1.5 | 20 | 49.4 | 0 | 0 | 1004 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:40 | 28.8 | 1.5 | 19.8 | 49.9 | 0 | 0 | 1004 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:45 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1004 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:57 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1004 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:01 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 1004 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:05 | 0 | 3 | 19.5 | 77.5 | 0 | 0 | 1004 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:08 | 0 | 1.6 | 19.6 | 78.8 | 0 | 0 | 1004 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:11 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1004 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:14 | 0 | 2.4 | 19.7 | 77.9 | 0 | 0 | 1004 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:21 | 0.2 | 2 | 19.5 | 78.3 | 0 | 0 | 1004 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:47 | 0.3 | 1.8 | 19.5 | 78.4 | 0 | 0 | 1004 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:51 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1004 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:54 | 0.2 | 1.6 | 19.7 | 78.5 | 0 | 0 | 1004 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:59 | 0.3 | 2.4 | 19.5 | 77.8 | 0 | 0 | 1004 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:04 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1004 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:07 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1004 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:11 | 0 | 2.5 | 19.6 | 77.9 | 0 | 0 | 1004 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-07-13
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 17 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:05 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1001 | 0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:10 | 0.2 | 1 | 20 | 78.8 | 0 | 0 | 1001 | -0.66 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:12 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1001 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:14 | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1001 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:17 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 1001 | 0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:21 | 0 | 2 | 20.1 | 77.9 | 0 | 0 | 1001 | 0.45 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:24 | 28.6 | 1.7 | 19.7 | 50 | 0 | 0 | 1001 | -0.26 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:30 | 28.5 | 1.4 | 19.8 | 50.3 | 0 | 0 | 1001 | 0.55 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:35 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1001 | 0.77 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:47 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 1001 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:51 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1001 | 0.29 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:55 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 1001 | -0.67 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:58 | 0 | 1.7 | 19.8 | 78.5 | 0 | 0 | 1001 | 0.33 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:01 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1001 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:04 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 1001 | 0.68 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:11 | 0.3 | 2.1 | 19.2 | 78.4 | 0 | 0 | 1001 | 0.47 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:37 | 0.2 | 1.8 | 19.9 | 78.1 | 0 | 0 | 1001 | -0.45 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:41 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1001 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:44 | 0.3 | 1.5 | 19.8 | 78.4 | 0 | 0 | 1001 | 0.03 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:49 | 0.4 | 2 | 19.2 | 78.4 | 0 | 0 | 1001 | 0.18 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:54 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1001 | 0.43 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:57 | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 1001 | -0.5 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:01 | 0 | 2.2 | 19.3 | 78.5 | 0 | 0 | 1001 | 0.42 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-07-20
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:52 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1003 | 0.69 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:57 | 0.3 | 1.1 | 19.9 | 78.7 | 0 | 0 | 1003 | 0.23 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:59 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 1003 | 0.24 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:02 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1003 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:04 | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 1003 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:08 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 1003 | 0.87 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:11 | 28.4 | 2 | 19 | 50.6 | 0 | 0 | 1003 | 0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:16 | 28 | 1.6 | 19.2 | 51.2 | 0 | 0 | 1003 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:22 | 0 | 1.7 | 19.3 | 79 | 0 | 0 | 1003 | 0.71 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:34 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 1003 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:38 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1003 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:42 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1003 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:45 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 1003 | 0.48 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:48 | 0 | 2.3 | 19.3 | 78.4 | 0 | 0 | 1003 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:51 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1003 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:58 | 0.2 | 2 | 20 | 77.8 | 0 | 0 | 1003 | 0.24 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:24 | 0.4 | 1.9 | 19.8 | 77.9 | 0 | 0 | 1003 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:28 | 0 | 2.3 | 19.3 | 78.4 | 0 | 0 | 1003 | 0.74 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:31 | 0.3 | 1.7 | 19.5 | 78.5 | 0 | 0 | 1003 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:26 | 0.3 | 2.4 | 19.8 | 77.5 | 0 | 0 | 1003 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:41 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 1003 | 0.85 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:44 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1003 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:48 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 1003 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-07-27
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 17 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:19 | 0 | 1.7 | 19.9 | 78.4 | 0 | 0 | 1006 | 0.53 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:24 | 0.2 | 1.4 | 20 | 78.4 | 0 | 0 | 1006 | -0.51 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:25 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1006 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:27 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 1006 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:31 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1006 | 0.57 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:35 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 1006 | 0.53 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:38 | 28 | 1.8 | 19.5 | 50.7 | 0 | 0 | 1006 | 0.48 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:44 | 27.5 | 1.4 | 19.7 | 51.4 | 0 | 0 | 1006 | 0.6 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:49 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1006 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:01 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1006 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:05 | 0 | 1.1 | 19.3 | 79.6 | 0 | 0 | 1006 | 0.33 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:09 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 1006 | -0.66 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:12 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1006 | 0.39 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:15 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1006 | 0.41 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:18 | 0 | 2.9 | 19.7 | 77.4 | 0 | 0 | 1006 | 0.88 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:25 | 0.3 | 2.5 | 19.8 | 77.4 | 0 | 0 | 1006 | 0.46 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:51 | 0.5 | 2 | 19.9 | 77.6 | 0 | 0 | 1006 | -0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:55 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1006 | 0.45 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:58 | 0.2 | 1.6 | 19.6 | 78.6 | 0 | 0 | 1006 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:03 | 0.4 | 2.3 | 19.4 | 77.9 | 0 | 0 | 1006 | 0.46 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:08 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1006 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:11 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1006 | -0.66 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:15 | 0 | 2.3 | 19.3 | 78.4 | 0 | 0 | 1006 | 0.41 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-07-24
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 16 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:30 | 50.1 | 37.9 | 0.9 | 11.1 | 8 | 6 | 1007 | 170 |  | Engine running 390 KW
GV1 |  | 37.9 | 25.9 | 1.5 | 34.7 | 6 | 6 | 1007 | -0.41 |  | OFF
GV3 |  | 54.6 | 36.8 | 0.4 | 8.2 | 2 | 3 | 1007 | -27.54 |  | Open Full
GV4 |  | 46 | 36 | 1.2 | 16.8 | 5 | 6 | 1007 | -5.54 |  | Left Cracked
GV6 |  | 46.5 | 36.5 | 1.1 | 15.9 | 9 | 8 | 1007 | -5.89 |  | Cracked Open
GV7 |  | 38.9 | 34.5 | 2.6 | 24 | 4 | 11 | 1007 | -0.01 |  | Off Low Gas high o2
GV8 |  | 36.2 | 32.5 | 2.5 | 28.8 | 8 | 6 | 1007 | -0.04 |  | Off Low Gas high o3
GV9 |  | 53 | 37.4 | 0.3 | 9.3 | 6 | 3 | 1007 | -27.45 |  | Open Full
GV10 |  | 39.6 | 35.2 | 1.7 | 23.5 | 5 | 1 | 1007 | -0.08 |  | Off
GV11 |  | 51.2 | 36.9 | 1 | 10.9 | 6 | 4 | 1007 | -7.79 | -11.28 | Reg Cracked open
GV12+R3 Manifold |  | 52.3 | 37 | 0.4 | 10.3 | 6 | 10 | 1007 | -27.55 |  | Open Full
GV12 |  | 53 | 37.5 | 0.3 | 9.2 | 5 | 10 | 1007 | -27.41 |  | Open Full
R3 |  | 51.8 | 36.6 | 0.4 | 11.2 | 7 | 8 | 1007 | -27.63 |  | Open Full
GV13 |  | 2.8 | 4.2 | 19 | 74 | 8 | 1 | 1007 | -0.12 |  | Left Closed
GV14 |  | 51.2 | 36.2 | 0.2 | 12.4 | 4 | 5 | 1007 | -27.24 |  | Open Full
GV15 |  | 50.9 | 37 | 0.4 | 11.7 | 5 | 6 | 1007 | -27.56 |  | Open Full
GV16 |  | 38 | 37.5 | 0.5 | 24 | 1 | 8 | 1007 | 0.08 |  | Left Closed
GV17+LC4 Manifold |  | 47 | 36.5 | 2.5 | 14 | 4 | 9 | 1007 | 0.04 |  | Off at Manifold Gas drops quick.
GV17 |  | 45.6 | 37.2 | 2 | 15.2 | 2 | 5 | 1007 | 0.04 |  | Open Full at Well
LC4 |  | 48 | 36 | 3.5 | 12.5 | 6 | 11 | 1007 | -0.05 |  | Open Full at well
GV18 |  | 51.9 | 36.9 | 0.5 | 10.7 | 10 | 6 | 1007 | -27.59 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.5 | 35.2 | 1.9 | 16.4 | 8 | 10 | 1007 | -0.32 |  | Off gas drops off quick.
GV23 |  | 50.5 | 36.5 | 0.3 | 12.7 | 6 | 6 | 1007 | -27.49 |  | Open Full
GV24 |  | 50.8 | 37 | 0.4 | 11.8 | 4 | 5 | 1007 | -27.89 |  | Open Full
GV25 |  | 40 | 36.9 | 1.9 | 21.2 | 10 | 1 | 1007 | -0.41 |  | Left Closed
GV26 + 27 Manifold |  | 52 | 37.4 | 0.5 | 10.1 | 8 | 10 | 1007 | -27.5 |  | Open Full
GV28+ 29 Manifold |  | 51.8 | 36.5 | 0.4 | 11.3 | 6 | 6 | 1007 | -27.49 |  | Open Full
GV26 |  | 52.2 | 36.4 | 0.3 | 11.1 | 5 | 13 | 1007 | -27.88 |  | Open Full
GV27 |  | 51.8 | 37.8 | 0.6 | 9.8 | 10 | 6 | 1007 | -27.34 |  | Open Full
GV28 |  | 52 | 36 | 0.3 | 11.7 | 5 | 8 | 1007 | -27.53 |  | Open Full
GV29 |  | 51.6 | 37.2 | 0.5 | 10.7 | 10 | 4 | 1007 | -27.43 |  | Open Full
GVA |  | 36.5 | 30 | 2.9 | 30.6 | 4 | 6 | 1007 | 0 |  | Off Low gas
B+C Manifold |  | 50.6 | 37 | 0.5 | 11.9 | 6 | 10 | 1007 | -27.55 |  | Open Full
GV B |  | 51.5 | 37 | 0.6 | 10.9 | 5 | 10 | 1007 | -27.59 |  | Open Full
GV C |  | 50.2 | 36.8 | 0.2 | 12.8 | 7 | 9 | 1007 | -27.46 |  | Open Full
GV30 |  | 52.6 | 36.4 | 1 | 10 | 10 | 6 | 1007 | -10.25 | -13.98 | cracked open
GV31 |  | 50 | 36.5 | 1.1 | 12.4 | 6 | 6 | 1007 | -11.68 | -14.78 | Cracked Open
GV32 |  | 49.9 | 37 | 1 | 12.1 | 8 | 14 | 1007 | -10.87 | -13.69 | Cracked Open
GV33 |  | 50.3 | 35.9 | 1 | 12.8 | 9 | 9 | 1007 | -10.23 | -14.25 | Cracked Open
GV34 |  | 47.8 | 36.5 | 1.1 | 14.6 | 4 | 1 | 1007 | -4.55 |  | Cracked Open
GV 35 (New Well) |  | 24.8 | 27 | 1.5 | 46.7 | 6 | 6 | 1007 | -0.02 |  | Left Closed
GV 36 (New Well) |  | 31.2 | 26.9 | 4.8 | 37.1 | 8 | 3 | 1007 | -0.01 |  | OFF low gas.
GV 37 (New Well) |  | 42.9 | 37 | 1.7 | 18.4 | 9 | 10 | 1007 | -0.02 |  | Reg closed hign o2 low gas
GV 38 (New Well) |  | 45.5 | 36 | 1.1 | 17.4 | 7 | 11 | 1007 | -6.56 |  | Cracked Open
GV 39 (New Well) |  | 45.9 | 36.4 | 1 | 16.7 | 5 | 9 | 1007 | -6.87 |  | Cracked Open
GV 40 (New Well) |  | 46.2 | 36.6 | 1.1 | 16.1 | 8 | 4 | 1007 | -6.21 |  | Cracked Open
GV 41 (New Well) |  | 45.9 | 36 | 1.1 | 17 | 11 | 7 | 1007 | -6.99 |  | Cracked Open
GV 42 (New Well) |  | 36.9 | 33.2 | 2 | 27.9 | 12 | 8 | 1007 | -0.04 |  | Off Low Gas
GV 43 (New Well) |  | 46 | 36.2 | 1.1 | 16.7 | 6 | 5 | 1007 | -6.58 |  | Cracked open
GV 44 (New Well) |  | 39 | 36.2 | 1.5 | 23.3 | 8 | 5 | 1007 | -0.29 |  | Off Low gas
GV 45 (New Well) |  | 45.8 | 36 | 1 | 17.2 | 6 | 8 | 1007 | -5.87 |  | Cracked Open
GV 46 (New Well) |  | 51.2 | 36.9 | 0.2 | 11.7 | 1 | 7 | 1007 | -27.59 |  | Open Full
GV 47 (New Well) |  | 47 | 36.5 | 1.1 | 15.4 | 7 | 9 | 1007 | -6.59 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 4 | 4 | 1007 | -27.41 |  | Open Full
GV 49 (New Well) |  | 41.9 | 36.8 | 2.3 | 19 | 9 | 8 | 1007 | 0.08 |  | Reg closed hign o2
LC1B |  | 37 | 33 | 1.9 | 28.1 | 6 | 5 | 1007 | -0.58 |  | OFF
LC2R? |  | 52.2 | 37 | 0.2 | 10.6 | 8 | 6 | 1007 | -27.49 |  | Open Full
GV 2.1 |  | 51.6 | 36.9 | 0.2 | 11.3 | 6 | 10 | 1007 | -27.39 |  | Open Full
GV 2.2+ LC2B MAN |  | 37 | 30.9 | 7 | 25.1 | 6 | 10 | 1007 | -0.03 |  | Left Closed
GV 2.2 |  | 37.5 | 29.8 | 4 | 28.7 | 5 | 10 | 1007 | -0.04 |  | Left Closed
LC2B |  | 34.5 | 31.9 | 8 | 25.6 | 7 | 10 | 1007 | -0.08 |  | Left Closed
GV / LC3.1 + LC3 MAN |  | 48 | 36.5 | 1 | 14.5 | 8 | 2 | 1007 | -10.99 |  | Left Open Half Way
LC3.1 |  | 48 | 36.5 | 1 | 14.5 | 8 | 2 | 1007 | -10.99 |  | Left open half way
LC3 |  | 41.5 | 35.8 | 2.9 | 19.8 | 11 | 4 | 1007 | -0.06 |  | OFF
LC4B |  | 48.5 | 36.9 | 1.4 | 13.2 | 14 | 6 | 1007 | -6.38 |  | Left Cracked Open
R1 + R1B Manifold |  | 50.2 | 36.9 | 0.7 | 12.2 | 9 | 5 | 1007 | -27.69 |  | Open Full
R1 |  | 47.9 | 36.5 | 1.1 | 14.5 | 7 | 3 | 1007 | -8.78 |  | Cracked Open
R1B |  | 51 | 37.9 | 0.3 | 10.8 | 14 | 7 | 1007 | -27.88 |  | Open Full
R2B |  | 51.2 | 36.5 | 0.4 | 11.9 | 10 | 6 | 1007 | -27.46 |  | Open Full
R4B |  | 43.9 | 36.5 | 2.5 | 17.1 | 9 | 5 | 1007 | 0.39 |  | Left closed
R6B |  | 51.2 | 36.9 | 0.2 | 11.7 | 8 | 6 | 1007 | -27.49 |  | Open Full
LC5 |  | 46 | 34.1 | 2.1 | 17.8 | 6 | 8 | 1007 | -0.39 |  | Left Off ( Gas drops quick)
LC6 |  | 46.9 | 35.6 | 2.5 | 15 | 5 | 7 | 1007 | -0.21 |  | Left Off ( Gas drops quick)
LC6B |  | 51.2 | 36.9 | 0.4 | 11.5 | 2 | 9 | 1007 | -27.49 |  | Open Full
PW1 |  | 2.6 | 1.7 | 9.2 | 86.5 | 8 | 4 | 1007 | -0.39 |  | Left Off
PW2 |  | 35.6 | 19.5 | 2.8 | 42.1 | 7 | 11 | 1007 | -0.65 |  | Left Off
PW3 |  | 30.4 | 20 | 3.5 | 46.1 | 9 | 10 | 1007 | -0.19 |  | Left Off
PW4 |  | 46.9 | 32.2 | 1.4 | 19.5 | 9 | 9 | 1007 | -6.98 |  | Cracked Open
PW5 |  | 36.2 | 27.9 | 1.2 | 34.7 | 7 | 6 | 1007 | -0.47 |  | Left Off
PW6 |  | 36.4 | 25.9 | 2.5 | 35.2 | 6 | 3 | 1007 | -0.56 |  | Left Off
Flare | 13:45 | 50.5 | 38 | 0.8 | 10.7 | 8 | 6 | 1007 | 170 |  | Engine running 395 KW. Flow 425m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## August 2017
Date | 2017-08-03
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 15 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.3 | 1.3 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:52 | 0 | 1 | 19.8 | 79.2 | 0 | 0 | 1002 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 1002 | -0.49 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1002 | -0.56 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1002 | 0.24 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 28.4 | 1.6 | 19.6 | 50.4 | 0 | 0 | 1002 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 27.9 | 1.2 | 19.5 | 51.4 | 0 | 0 | 1002 | -0.28 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1002 | -0.63 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | 0.11 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1002 | 0.78 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 1002 | -0.15 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1002 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1002 | -0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1002 | 0.21 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.2 | 2.1 | 19.6 | 78.1 | 0 | 0 | 1002 | -0.75 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.4 | 2.3 | 19.5 | 77.8 | 0 | 0 | 1002 | -0.63 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2 | 20 | 78 | 0 | 0 | 1002 | 0.54 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.3 | 1.8 | 19.8 | 78.1 | 0 | 0 | 1002 | -0.96 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.3 | 2.5 | 19.6 | 77.6 | 0 | 0 | 1002 | -0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1002 | 0.34 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | -0.44 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 2.2 | 20 | 77.8 | 0 | 0 | 1002 | 0.25 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-08-10
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1000 | -0.35 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.2 | 1.2 | 19.8 | 78.8 | 0 | 0 | 1000 | 0.76 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:11 | 0 | 1.1 | 19.6 | 79.3 | 0 | 0 | 1000 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:13 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 1000 | -0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1000 | 0.52 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 1000 | 0.48 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 28.6 | 1.5 | 19.3 | 50.6 | 0 | 0 | 1000 | -0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28 | 1.3 | 19.5 | 51.2 | 0 | 0 | 1000 | 0.36 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1000 | -0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1000 | 0.16 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1000 | 0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1000 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1000 | 0.35 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 2 | 19.3 | 78.7 | 0 | 0 | 1000 | -0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1000 | 0.48 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 2.6 | 19.7 | 77.4 | 0 | 0 | 1000 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.3 | 2.1 | 19.6 | 78 | 0 | 0 | 1000 | 0.25 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2.3 | 20.1 | 77.6 | 0 | 0 | 1000 | 0.69 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.2 | 1.5 | 19.5 | 78.8 | 0 | 0 | 1000 | -0.17 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.4 | 2.6 | 19.7 | 77.3 | 0 | 0 | 1000 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1000 | 0.39 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1000 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1000 | 0.28 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-08-17
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 13 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:52 | 0 | 1.2 | 20 | 78.8 | 0 | 0 | 1004 | -0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:57 | 0.3 | 1.3 | 19.9 | 78.5 | 0 | 0 | 1004 | 0.85 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:00 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 1004 | 0.75 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:02 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 1004 | 0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:04 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1004 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:08 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1004 | -0.11 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:11 | 28.5 | 1.7 | 19.5 | 50.3 | 0 | 0 | 1004 | 0.56 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:16 | 27.8 | 1.4 | 19.6 | 51.2 | 0 | 0 | 1004 | 0.47 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:22 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 1004 | -0.18 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:34 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1004 | 0.24 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:38 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 1004 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:42 | 0 | 2.4 | 19.3 | 78.3 | 0 | 0 | 1004 | 0.75 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:45 | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 1004 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:48 | 0 | 2.1 | 19.7 | 78.2 | 0 | 0 | 1004 | 0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:51 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 1004 | 0.87 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:58 | 0.4 | 2.4 | 19.6 | 77.6 | 0 | 0 | 1004 | 0.98 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:24 | 0.4 | 2.5 | 19.3 | 77.8 | 0 | 0 | 1004 | -0.14 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:28 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1004 | 0.26 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:31 | 0.3 | 1.4 | 19.8 | 78.5 | 0 | 0 | 1004 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:26 | 0.3 | 2.9 | 20 | 76.8 | 0 | 0 | 1004 | -0.11 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:41 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1004 | 0.32 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:44 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1004 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:48 | 0 | 2.6 | 19.4 | 78 | 0 | 0 | 1004 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-08-24
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 14 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:52 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 999 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:57 | 0.2 | 1.4 | 19.5 | 78.9 | 0 | 0 | 999 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:59 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 999 | 0.58 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 12:01 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 999 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 12:04 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 999 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 12:08 | 0 | 2.7 | 19.6 | 77.7 | 0 | 0 | 999 | 0.84 | 1 | 10 | 0.5 | 5
BK BH 8 | 12:11 | 28.8 | 1.5 | 19.5 | 50.2 | 0 | 0 | 999 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:17 | 28.5 | 1.8 | 19.9 | 49.8 | 0 | 0 | 999 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:22 | 0 | 1.6 | 20 | 78.4 | 0 | 0 | 999 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:34 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 999 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:38 | 0 | 1.7 | 19.4 | 78.9 | 0 | 0 | 999 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:42 | 0 | 2.6 | 19.3 | 78.1 | 0 | 0 | 999 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:45 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 999 | 0.41 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:48 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 999 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:51 | 0 | 2 | 19.7 | 78.3 | 0 | 0 | 999 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:58 | 0.3 | 2.4 | 19.9 | 77.4 | 0 | 0 | 999 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:24 | 0.2 | 2.2 | 19.8 | 77.8 | 0 | 0 | 999 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:28 | 0 | 2.8 | 19.5 | 77.7 | 0 | 0 | 999 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:31 | 0.4 | 1.9 | 19.3 | 78.4 | 0 | 0 | 999 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:36 | 0.3 | 3 | 20 | 76.7 | 0 | 0 | 999 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:41 | 0 | 2.6 | 20.1 | 77.3 | 0 | 0 | 999 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:44 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 999 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:48 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 999 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-08-31
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 16 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:05 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 1001 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:10 | 0.3 | 1.5 | 20 | 78.2 | 0 | 0 | 1001 | -0.62 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:12 | 0 | 1.7 | 20.1 | 78.2 | 0 | 0 | 1001 | 0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:14 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1001 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:17 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1001 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:21 | 0 | 2.5 | 19.4 | 78.1 | 0 | 0 | 1001 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:24 | 28.6 | 1.1 | 19.7 | 50.6 | 0 | 0 | 1001 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:30 | 28.4 | 1.6 | 19.3 | 50.7 | 0 | 0 | 1001 | 0.46 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:35 | 0 | 1.9 | 19.5 | 78.6 | 0 | 0 | 1001 | 0.69 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:47 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1001 | -0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:51 | 0 | 1.9 | 19.9 | 78.2 | 0 | 0 | 1001 | 0.24 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:55 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1001 | -0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:58 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1001 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:01 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1001 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:04 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 1001 | 0.58 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:11 | 0.4 | 2.1 | 19.7 | 77.8 | 0 | 0 | 1001 | 0.77 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:37 | 0.3 | 2 | 19.1 | 78.6 | 0 | 0 | 1001 | -0.96 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:41 | 0 | 2.5 | 19 | 78.5 | 0 | 0 | 1001 | 0.38 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:44 | 0.4 | 1.5 | 20 | 78.1 | 0 | 0 | 1001 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:49 | 0.3 | 3.2 | 19.9 | 76.6 | 0 | 0 | 1001 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:54 | 0 | 2.8 | 19.5 | 77.7 | 0 | 0 | 1001 | 0.75 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:57 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 1001 | -0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:01 | 0 | 3 | 19.8 | 77.2 | 0 | 0 | 1001 | 0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date |  | 2017-08-21
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 15 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:10 | 50.4 | 38 | 0.8 | 10.8 | 9 | 5 | 111 | 165 |  | Engine running 400 KW
GV1 |  | 36.9 | 24.5 | 1.4 | 37.2 | 5 | 6 | 111 | -0.32 |  | OFF
GV3 |  | 55 | 37 | 0.3 | 7.7 | 3 | 5 | 111 | -25.88 |  | Open Full
GV4 |  | 46.1 | 35.8 | 1.1 | 17 | 6 | 9 | 111 | -4.88 |  | Left Cracked
GV6 |  | 46.7 | 36.9 | 1.2 | 15.2 | 9 | 2 | 111 | -4.89 |  | Cracked Open
GV7 |  | 38.1 | 34.2 | 2.4 | 25.3 | 6 | 4 | 111 | -0.05 |  | Off Low Gas high o2
GV8 |  | 37.9 | 33.6 | 2.8 | 25.7 | 4 | 8 | 111 | -0.08 |  | Off Low Gas high o3
GV9 |  | 52.8 | 37 | 0.4 | 9.8 | 8 | 9 | 111 | -25.47 |  | Open Full
GV10 |  | 40 | 35.8 | 1.5 | 22.7 | 5 | 6 | 111 | -0.08 |  | Off
GV11 |  | 45.2 | 36.5 | 1.2 | 17.1 | 10 | 8 | 111 | -12.35 | -6.55 | Reg Closed to cracked
GV12+R3 Manifold |  | 52.8 | 37.5 | 0.3 | 9.4 | 7 | 11 | 111 | -25.55 |  | Open Full
GV12 |  | 53.2 | 37.8 | 0.3 | 8.7 | 5 | 12 | 111 | -25.74 |  | Open Full
R3 |  | 52 | 37 | 0.4 | 10.6 | 7 | 9 | 111 | -25.39 |  | Open Full
GV13 |  | 2.9 | 4.5 | 19.5 | 73.1 | 7 | 3 | 111 | -0.11 |  | Left Closed
GV14 |  | 51.8 | 36.5 | 0.3 | 11.4 | 9 | 6 | 111 | -25.78 |  | Open Full
GV15 |  | 51.3 | 37.8 | 0.4 | 10.5 | 5 | 8 | 111 | -25.39 |  | Open Full
GV16 |  | 37.5 | 38.9 | 0.4 | 23.2 | 2 | 5 | 111 | 0.08 |  | Left Closed
GV17+LC4 Manifold |  | 47.3 | 36.8 | 2.6 | 13.3 | 5 | 10 | 111 | -0.05 |  | Off at Manifold Gas drops quick.
GV17 |  | 46 | 37.4 | 2.3 | 14.3 | 3 | 5 | 111 | -0.04 |  | Open Full at Well
LC4 |  | 48.2 | 36.2 | 3.2 | 12.4 | 7 | 12 | 111 | -0.05 |  | Open Full at well
GV18 |  | 51 | 36.2 | 0.3 | 12.5 | 11 | 5 | 111 | -25.87 |  | Left open Full
Point: GV19; %: 100 |  |  | N/A Going to decommission.
GV 22 |  | 46.2 | 35.2 | 1.6 | 17 | 7 | 9 | 111 | -0.25 |  | Off gas drops off quick.
GV23 |  | 50.8 | 36.7 | 0.2 | 12.3 | 9 | 5 | 111 | -25.47 |  | Open Full
GV24 |  | 50.5 | 36.9 | 0.5 | 12.1 | 4 | 6 | 111 | -25.93 |  | Open Full
GV25 |  | 41.2 | 37 | 1.8 | 20 | 10 | 7 | 111 | -0.35 |  | Left Closed
GV26 + 27 Manifold |  | 52.3 | 37 | 0.4 | 10.3 | 7 | 11 | 111 | -25.47 |  | Open Full
GV28+ 29 Manifold |  | 51.5 | 36.9 | 0.6 | 11 | 5 | 9 | 111 | -25.62 |  | Open Full
GV26 |  | 52.5 | 36.8 | 0.2 | 10.5 | 6 | 12 | 111 | -25.57 |  | Open Full
GV27 |  | 51.9 | 37.6 | 0.5 | 10 | 8 | 8 | 111 | -25.38 |  | Open Full
GV28 |  | 52 | 36.5 | 0.3 | 11.2 | 4 | 10 | 111 | -25.88 |  | Open Full
GV29 |  | 51.3 | 37 | 0.7 | 11 | 8 | 5 | 111 | -25.5 |  | Open Full
GVA |  | 36.4 | 30.6 | 2.5 | 30.5 | 5 | 9 | 111 | 0 |  | Off Low gas
B+C Manifold |  | 50.4 | 36.8 | 0.6 | 12.2 | 7 | 9 | 111 | -25.55 |  | Open Full
GV B |  | 51 | 37.1 | 0.7 | 11.2 | 6 | 9 | 111 | -25.75 |  | Open Full
GV C |  | 50 | 36.5 | 0.4 | 13.1 | 7 | 9 | 111 | -25.41 |  | Open Full
GV30 |  | 48.9 | 36.9 | 1.1 | 13.1 | 2 | 8 | 111 | -9.96 | -12.88 | cracked open
GV31 |  | 49.6 | 35.9 | 1.1 | 13.4 | 5 | 9 | 111 | -9.88 | -12.17 | Cracked Open
GV32 |  | 48 | 36.2 | 1 | 14.8 | 3 | 5 | 111 | -9.1 | -12.18 | Cracked Open
GV33 |  | 49 | 36 | 1 | 14 | 5 | 6 | 111 | -9.68 | -12.14 | Cracked Open
GV34 |  | 46.2 | 36.9 | 1.2 | 15.7 | 7 | 7 | 111 | -4.99 |  | Cracked Open
GV 35 (New Well) |  | 25.9 | 28.5 | 1.6 | 44 | 8 | 5 | 111 | -0.02 |  | Left Closed
GV 36 (New Well) |  | 33.8 | 30 | 4.6 | 31.6 | 6 | 6 | 111 | -0.04 |  | OFF low gas.
GV 37 (New Well) |  | 40.5 | 36.9 | 1.5 | 21.1 | 10 | 7 | 111 | -0.02 |  | closed hign o2 low gas
GV 38 (New Well) |  | 45.9 | 36.8 | 1.2 | 16.1 | 8 | 10 | 111 | -6.88 |  | Cracked Open
GV 39 (New Well) |  | 45.6 | 36.4 | 1.1 | 16.9 | 9 | 4 | 111 | -6.67 |  | Cracked Open
GV 40 (New Well) |  | 46 | 36.5 | 1 | 16.5 | 5 | 9 | 111 | -6.23 |  | Cracked Open
GV 41 (New Well) |  | 46.2 | 36.2 | 1.2 | 16.4 | 10 | 6 | 111 | -6.58 |  | Cracked Open
GV 42 (New Well) |  | 37.5 | 34.2 | 1.8 | 26.5 | 11 | 8 | 111 | -0.06 |  | Off Low Gas
GV 43 (New Well) |  | 46.8 | 36.5 | 1.2 | 15.5 | 9 | 5 | 111 | -6.88 |  | Cracked open
GV 44 (New Well) |  | 40 | 36.5 | 1.4 | 22.1 | 6 | 5 | 111 | -0.35 |  | Off Low gas
GV 45 (New Well) |  | 46.2 | 36.2 | 1 | 16.6 | 4 | 8 | 111 | -5.68 |  | Cracked Open
GV 46 (New Well) |  | 52.3 | 37.2 | 0.3 | 10.2 | 1 | 7 | 111 | -25.59 |  | Open Full
GV 47 (New Well) |  | 46.9 | 36.5 | 1 | 15.6 | 7 | 9 | 111 | -6.95 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 4 | 11 | 111 | -25.41 |  | Open Full
GV 49 (New Well) |  | 42.2 | 37 | 1.8 | 19 | 5 | 12 | 111 | -0.08 |  | Reg closed hign o2
LC1B |  | 36.9 | 34.5 | 2 | 26.6 | 8 | 6 | 111 | -0.69 |  | OFF
LC2R? |  | 51.8 | 37.5 | 0.3 | 10.4 | 6 | 8 | 111 | -25.59 |  | Open Full
GV 2.1 |  | 52.3 | 37 | 0.4 | 10.3 | 10 | 9 | 111 | -25.68 |  | Open Full
GV 2.2+ LC2B MAN |  | 36.9 | 31.2 | 6.8 | 25.1 | 7 | 11 | 111 | -0.04 |  | Left Closed
GV 2.2 |  | 37.9 | 30 | 4.5 | 27.6 | 8 | 11 | 111 | -0.04 |  | Left Closed
LC2B |  | 34.9 | 33.5 | 7.4 | 24.2 | 6 | 9 | 111 | -0.06 |  | Left Closed
GV / LC3.1 + LC3 MAN |  | 48.5 | 36.8 | 1 | 13.7 | 10 | 3 | 111 | -11.06 |  | Left Open Half Way
LC3.1 |  | 48.5 | 36.8 | 1 | 13.7 | 10 | 3 | 111 | -11.06 |  | Left open half way
LC3 |  | 41.3 | 36.5 | 2.5 | 19.7 | 6 | 9 | 111 | -0.09 |  | OFF
LC4B |  | 48 | 36.9 | 1.3 | 13.8 | 7 | 8 | 111 | -6.55 |  | Left Cracked Open
R1 + R1B Manifold |  | 51.6 | 37.5 | 0.6 | 10.3 | 10 | 6 | 111 | -25.49 |  | Open Full
R1 |  | 48 | 36.8 | 1 | 14.2 | 8 | 4 | 111 | -7.89 |  | Cracked Open
R1B |  | 51.6 | 38 | 0.5 | 9.9 | 12 | 8 | 111 | -25.99 |  | Open Full
R2B |  | 50.2 | 36.9 | 0.3 | 12.6 | 5 | 10 | 111 | -25.41 |  | Open Full
R4B |  | 44.5 | 36.9 | 2.6 | 16 | 6 | 6 | 111 | 0.12 |  | Left closed
R6B |  | 51.6 | 37 | 0.2 | 11.2 | 9 | 2 | 111 | -25.58 |  | Open Full
LC5 |  | 46.9 | 34.5 | 2.3 | 16.3 | 8 | 5 | 111 | -0.35 |  | Left Off ( Gas drops quick)
LC6 |  | 45.8 | 36 | 2.4 | 15.8 | 11 | 4 | 111 | -0.24 |  | Left Off ( Gas drops quick)
LC6B |  | 51.6 | 37.2 | 0.5 | 10.7 | 4 | 9 | 111 | -25.63 |  | Open Full
PW1 |  | 2.8 | 1.5 | 9 | 86.7 | 10 | 5 | 111 | -0.35 |  | Left Off
PW2 |  | 36 | 19.6 | 2.5 | 41.9 | 9 | 5 | 111 | -0.57 |  | Left Off
PW3 |  | 32.5 | 19.9 | 3.2 | 44.4 | 5 | 8 | 111 | -0.15 |  | Left Off
PW4 |  | 47.5 | 33.6 | 1.1 | 17.8 | 5 | 7 | 111 | -7.05 |  | Cracked Open
PW5 |  | 36.8 | 26.9 | 1.2 | 35.1 | 6 | 10 | 111 | -0.53 |  | Left Off
PW6 |  | 37 | 26.5 | 2.4 | 34.1 | 8 | 6 | 111 | -0.58 |  | Left Off
Flare | 13:35 | 50.5 | 38 | 0.7 | 10.8 | 9 | 5 | 111 | 165 |  | Engine running 400 KW. Flow 425m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## Sept 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-09-07
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 13 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:52 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 1004 | -0.36 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:57 | 0.2 | 1.2 | 19.9 | 78.7 | 0 | 0 | 1004 | 0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:59 | 0 | 1.5 | 19.6 | 78.9 | 0 | 0 | 1004 | -0.12 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 12:01 | 0 | 0.5 | 19.8 | 79.7 | 0 | 0 | 1004 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 12:04 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1004 | 0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 12:08 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1004 | -0.52 | 1 | 10 | 0.5 | 5
BK BH 8 | 12:11 | 28.5 | 1.4 | 19.8 | 50.3 | 0 | 0 | 1004 | 0.65 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:17 | 28.6 | 1.9 | 19.9 | 49.6 | 0 | 0 | 1004 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:22 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1004 | -0.23 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:34 | 0 | 2.6 | 19.5 | 77.9 | 0 | 0 | 1004 | 0.64 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:38 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1004 | 0.57 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:42 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1004 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:45 | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1004 | 0.54 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:48 | 0 | 2.9 | 19.9 | 77.2 | 0 | 0 | 1004 | 0.84 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:51 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1004 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:58 | 0.3 | 2 | 19.8 | 77.9 | 0 | 0 | 1004 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:24 | 0.4 | 2.8 | 20 | 76.8 | 0 | 0 | 1004 | 0.58 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:28 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 1004 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:31 | 0.3 | 1.6 | 19.6 | 78.5 | 0 | 0 | 1004 | -0.25 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:36 | 0.3 | 3.5 | 19.7 | 76.5 | 0 | 0 | 1004 | 0.79 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:41 | 0 | 3 | 19.4 | 77.6 | 0 | 0 | 1004 | 0.28 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:44 | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1004 | -0.2 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:48 | 0 | 3.2 | 19.9 | 76.9 | 0 | 0 | 1004 | -0.11 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-09-14
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:06 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 1002 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:11 | 0.3 | 1 | 20 | 78.7 | 0 | 0 | 1002 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:12 | 0 | 1.3 | 19.7 | 79 | 0 | 0 | 1002 | 0.58 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:14 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1002 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:18 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:22 | 0 | 2 | 20 | 78 | 0 | 0 | 1002 | 0.84 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:25 | 28.2 | 1.6 | 19.8 | 50.4 | 0 | 0 | 1002 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:31 | 28.4 | 2 | 19.9 | 49.7 | 0 | 0 | 1002 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:36 | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 1002 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:48 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:52 | 0 | 2.5 | 19.7 | 77.8 | 0 | 0 | 1002 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:56 | 0 | 2.9 | 19.3 | 77.8 | 0 | 0 | 1002 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:59 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 1002 | 0.41 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:02 | 0 | 2.8 | 19.7 | 77.5 | 0 | 0 | 1002 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:05 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 1002 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:12 | 0.2 | 2.5 | 20 | 77.3 | 0 | 0 | 1002 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:38 | 0.3 | 2.7 | 19.8 | 77.2 | 0 | 0 | 1002 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:42 | 0 | 2.3 | 19.5 | 78.2 | 0 | 0 | 1002 | 0.78 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:45 | 0.4 | 1.9 | 19.6 | 78.1 | 0 | 0 | 1002 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:50 | 0.3 | 3.2 | 19.7 | 76.8 | 0 | 0 | 1002 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:55 | 0 | 2.8 | 19.5 | 77.7 | 0 | 0 | 1002 | 0.82 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:58 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1002 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:02 | 0 | 3.6 | 20 | 76.4 | 0 | 0 | 1002 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-09-21
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:27 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 999 | 0.79 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:32 | 0.4 | 0.8 | 20 | 78.8 | 0 | 0 | 999 | -0.69 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:34 | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 999 | 0.89 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:36 | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 999 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:39 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 999 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:43 | 0 | 1.8 | 19.7 | 78.5 | 0 | 0 | 999 | 0.94 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:46 | 28 | 1.5 | 19.9 | 50.6 | 0 | 0 | 999 | 0.71 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:52 | 28.1 | 2.3 | 20 | 49.6 | 0 | 0 | 999 | 0.9 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:57 | 0 | 1.1 | 19.3 | 79.6 | 0 | 0 | 999 | 0.87 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:09 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 999 | -0.88 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:13 | 0 | 2.6 | 19.4 | 78 | 0 | 0 | 999 | 0.62 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:17 | 0 | 3 | 19.8 | 77.2 | 0 | 0 | 999 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:20 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 999 | 0.56 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:23 | 0 | 3 | 20 | 77 | 0 | 0 | 999 | 0.74 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:26 | 0 | 2.2 | 19.9 | 77.9 | 0 | 0 | 999 | 1.13 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:33 | 0.4 | 2.4 | 19.9 | 77.3 | 0 | 0 | 999 | 0.99 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:59 | 0.2 | 2.8 | 19.8 | 77.2 | 0 | 0 | 999 | 0.68 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:03 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 999 | 0.81 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:06 | 0.4 | 1.5 | 20 | 78.1 | 0 | 0 | 999 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:11 | 0.2 | 3 | 19.7 | 77.1 | 0 | 0 | 999 | 0.89 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:16 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 999 | 0.34 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:19 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 999 | -0.58 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:23 | 0 | 3.2 | 19.9 | 76.9 | 0 | 0 | 999 | 0.87 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-09-25
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 11 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:30 | 49.8 | 38.2 | 0.7 | 11.3 | 8 | 4 | 997 | 160 |  | Engine running 400 KW
GV1 |  | 36.9 | 23.4 | 1.6 | 38.1 | 6 | 7 | 997 | -0.21 |  | OFF
GV3 |  | 54.2 | 37.8 | 0.2 | 7.8 | 2 | 9 | 997 | -26.35 |  | Open Full
GV4 |  | 46.2 | 36 | 1.2 | 16.6 | 10 | 9 | 997 | -4.99 |  | Left Cracked
GV6 |  | 45.9 | 37 | 1.1 | 16 | 8 | 4 | 997 | -4.98 |  | Cracked Open
GV7 |  | 36.9 | 32.8 | 2.5 | 27.8 | 4 | 3 | 997 | -0.01 |  | Off Low Gas high o2
GV8 |  | 37.4 | 33.2 | 2.6 | 26.8 | 7 | 5 | 997 | -0.08 |  | Off Low Gas high o3
GV9 |  | 51.9 | 36.9 | 0.2 | 11 | 9 | 8 | 997 | -26.39 |  | Open Full
GV10 |  | 40.4 | 36.2 | 1.4 | 22 | 3 | 9 | 997 | -0.07 |  | Off
GV11 |  | 47 | 36.8 | 1 | 15.2 | 5 | 10 | 997 | -6.58 | -8.14 | Regulated
GV12+R3 Manifold |  | 50.2 | 37.6 | 0.4 | 11.8 | 8 | 5 | 997 | -26.61 |  | Open Full
GV12 |  | 51 | 38 | 0.3 | 10.7 | 4 | 10 | 997 | -26.75 |  | Open Full
R3 |  | 49.6 | 37.1 | 0.4 | 12.9 | 10 | 2 | 997 | -26.41 |  | Open Full
GV13 |  | 2.6 | 4.8 | 19.2 | 73.4 | 8 | 6 | 997 | -0.04 |  | Left Closed
GV14 |  | 50 | 37 | 0.2 | 12.8 | 7 | 4 | 997 | -26.89 |  | Open Full
GV15 |  | 50.3 | 36.9 | 0.4 | 12.4 | 6 | 8 | 997 | -26.41 |  | Open Full
GV16 |  | 36.9 | 36.5 | 1 | 25.6 | 4 | 6 | 997 | 0.02 |  | Left Closed
GV17+LC4 Manifold |  | 47.5 | 36.5 | 2.5 | 13.5 | 7 | 9 | 997 | -0.04 |  | Off at Manifold Gas drops quick.
GV17 |  | 46.2 | 37.2 | 2.1 | 14.5 | 4 | 7 | 997 | -0.04 |  | Open Full at Well
LC4 |  | 48.4 | 36 | 3 | 12.6 | 9 | 11 | 997 | -0.05 |  | Open Full at well
GV18 |  | 50.1 | 36.5 | 0.2 | 13.2 | 10 | 6 | 997 | -26.55 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 46.9 | 34.8 | 1.5 | 16.8 | 8 | 7 | 997 | -0.29 |  | Off gas drops off quick.
GV23 |  | 50.1 | 36 | 0.4 | 13.5 | 10 | 10 | 997 | -26.57 |  | Open Full
GV24 |  | 49.9 | 36.5 | 0.3 | 13.3 | 6 | 8 | 997 | -26.53 |  | Open Full
GV25 |  | 42.6 | 35.2 | 1.9 | 20.3 | 9 | 5 | 997 | -0.27 |  | Left Closed
GV26 + 27 Manifold |  | 52 | 36.9 | 0.6 | 10.5 | 8 | 10 | 997 | -26.57 |  | Open Full
GV28+ 29 Manifold |  | 50 | 36.5 | 0.3 | 13.2 | 3 | 7 | 997 | -26.43 |  | Open Full
GV26 |  | 52.3 | 36.5 | 0.2 | 11 | 6 | 11 | 997 | -26.59 |  | Open Full
GV27 |  | 51.7 | 37.2 | 0.7 | 10.4 | 10 | 6 | 997 | -26.4 |  | Open Full
GV28 |  | 50.2 | 36.2 | 0.3 | 13.3 | 2 | 1 | 997 | -26.55 |  | Open Full
GV29 |  | 49.7 | 37.1 | 0.5 | 12.7 | 6 | 9 | 997 | -26.21 |  | Open Full
GVA |  | 37.2 | 30.8 | 2.6 | 29.4 | 4 | 6 | 997 | 0 |  | Off Low gas
B+C Manifold |  | 50.1 | 36.9 | 0.5 | 12.5 | 8 | 9 | 997 | -26.6 |  | Open Full
GV B |  | 50.8 | 37.1 | 0.6 | 11.5 | 6 | 10 | 997 | -26.71 |  | Open Full
GV C |  | 49.6 | 36.6 | 0.2 | 13.6 | 10 | 8 | 997 | -26.43 |  | Open Full
GV30 |  | 49 | 36.4 | 1 | 13.6 | 3 | 2 | 997 | -12.14 | -14.55 | cracked open
GV31 |  | 48.9 | 36.2 | 1 | 13.9 | 6 | 9 | 997 | -10.99 |  | Cracked Open
GV32 |  | 48.5 | 35.9 | 1.1 | 14.5 | 8 | 7 | 997 | -8.97 | -13.59 | Cracked Open
GV33 |  | 49.9 | 36.5 | 1 | 12.6 | 9 | 8 | 997 | -10.36 | -11.24 | Cracked Open
GV34 |  | 46.8 | 36 | 1.1 | 16.1 | 11 | 6 | 997 | -5.98 |  | Cracked Open
GV 35 (New Well) |  | 24.9 | 28.9 | 1.9 | 44.3 | 10 | 6 | 997 | -0.02 |  | Left Closed
GV 36 (New Well) |  | 32.4 | 30.2 | 4.9 | 32.5 | 6 | 7 | 997 | -0.04 |  | OFF low gas.
GV 37 (New Well) |  | 39.8 | 36 | 1.8 | 22.4 | 4 | 10 | 997 | -0.02 |  | closed hign o2 low gas
GV 38 (New Well) |  | 46 | 35.9 | 1.1 | 17 | 2 | 8 | 997 | -6.88 |  | Cracked Open
GV 39 (New Well) |  | 46.2 | 36.2 | 1 | 16.6 | 9 | 7 | 997 | -6.67 |  | Cracked Open
GV 40 (New Well) |  | 45.8 | 36.9 | 1.1 | 16.2 | 8 | 5 | 997 | -6.23 |  | Cracked Open
GV 41 (New Well) |  | 46.4 | 36 | 1 | 16.6 | 7 | 8 | 997 | -6.58 |  | Cracked Open
GV 42 (New Well) |  | 36.9 | 35.9 | 1.7 | 25.5 | 10 | 4 | 997 | -0.06 |  | Off Low Gas
GV 43 (New Well) |  | 47.1 | 36.9 | 1.1 | 14.9 | 11 | 6 | 997 | -6.88 |  | Cracked open
GV 44 (New Well) |  | 40.5 | 36.9 | 1.5 | 21.1 | 6 | 8 | 997 | -0.35 |  | Off Low gas
GV 45 (New Well) |  | 46 | 35.8 | 1.1 | 17.1 | 3 | 9 | 997 | -5.68 |  | Cracked Open
GV 46 (New Well) |  | 51.4 | 37.8 | 0.2 | 10.6 | 5 | 11 | 997 | -25.59 |  | Open Full
GV 47 (New Well) |  | 47.5 | 36.9 | 1.2 | 14.4 | 4 | 1 | 997 | -6.95 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 7 | 10 | 997 | -25.41 |  | Open Full
GV 49 (New Well) |  | 43.6 | 36.4 | 1.9 | 18.1 | 10 | 3 | 997 | -0.08 |  | Reg closed hign o2
LC1B |  | 36.4 | 35.8 | 2.6 | 25.2 | 10 | 7 | 997 | -0.69 |  | OFF
LC2R? |  | 51 | 36.9 | 0.2 | 11.9 | 6 | 9 | 997 | -25.59 |  | Open Full
GV 2.1 |  | 50.8 | 37.5 | 0.1 | 11.6 | 11 | 6 | 997 | -25.68 |  | Open Full
GV 2.2+ LC2B MAN |  | 37.9 | 32.2 | 6.1 | 23.8 | 10 | 13 | 997 | -0.04 |  | Left Closed
GV 2.2 |  | 39.9 | 30.8 | 4.1 | 25.2 | 12 | 14 | 997 | -0.04 |  | Left Closed
LC2B |  | 35.4 | 33.1 | 7.9 | 23.6 | 8 | 6 | 997 | -0.06 |  | Left Closed
GV / LC3.1 + LC3 MAN |  | 48.6 | 37 | 1 | 13.4 | 9 | 4 | 997 | -11.06 |  | Left Open Half Way
LC3.1 |  | 48.6 | 37 | 1 | 13.4 | 9 | 4 | 997 | -11.06 |  | Left open half way
LC3 |  | 42.3 | 36.8 | 2.7 | 18.2 | 6 | 9 | 997 | -0.09 |  | OFF
LC4B |  | 48.5 | 36.5 | 1.2 | 13.8 | 10 | 6 | 997 | -6.55 |  | Left Cracked Open
R1 + R1B Manifold |  | 51.8 | 37.3 | 0.7 | 10.2 | 11 | 6 | 997 | -25.49 |  | Open Full
R1 |  | 48.9 | 36.5 | 1 | 13.6 | 9 | 5 | 997 | -7.89 |  | Cracked Open
R1B |  | 52 | 38.2 | 0.6 | 9.2 | 14 | 8 | 997 | -25.99 |  | Open Full
R2B |  | 50.9 | 36.8 | 0.4 | 11.9 | 10 | 7 | 997 | -25.41 |  | Open Full
R4B |  | 43.8 | 37 | 2.5 | 16.7 | 6 | 8 | 997 | 0.12 |  | Left closed
R6B |  | 52.4 | 37.5 | 0.3 | 9.8 | 8 | 6 | 997 | -25.58 |  | Open Full
LC5 |  | 46.5 | 34.9 | 2.5 | 16.1 | 10 | 14 | 997 | -0.35 |  | Left Off ( Gas drops quick)
LC6 |  | 47 | 33 | 2.1 | 17.9 | 4 | 11 | 997 | -0.24 |  | Left Off ( Gas drops quick)
LC6B |  | 50.2 | 36.9 | 0.4 | 12.5 | 7 | 10 | 997 | -25.63 |  | Open Full
PW1 |  | 2.9 | 1.7 | 8.9 | 86.5 | 9 | 5 | 997 | -0.35 |  | Left Off
PW2 |  | 34.6 | 19.2 | 2.7 | 43.5 | 5 | 7 | 997 | -0.57 |  | Left Off
PW3 |  | 33.5 | 20 | 3.7 | 42.8 | 8 | 4 | 997 | -0.15 |  | Left Off
PW4 |  | 47.8 | 34 | 1.1 | 17.1 | 10 | 8 | 997 | -7.05 |  | Cracked Open
PW5 |  | 37 | 24.8 | 1.6 | 36.6 | 11 | 5 | 997 | -0.53 |  | Left Off
PW6 |  | 37.5 | 27.8 | 2.8 | 31.9 | 6 | 3 | 997 | -0.58 |  | Left Off
Flare | 14:00 | 49.8 | 38.2 | 0.6 | 11.4 | 8 | 4 | 997 | 165 |  | Engine running 400 KW. Flow 425m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## Oct 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-10-05
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:22 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 1001 | -0.96 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:27 | 0.2 | 0.5 | 19.7 | 79.6 | 0 | 0 | 1001 | 0.36 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:30 | 0 | 1 | 19.6 | 79.4 | 0 | 0 | 1001 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1001 | 0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:34 | 0 | 0.8 | 20.3 | 78.9 | 0 | 0 | 1001 | 0.87 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:38 | 0 | 1.2 | 19.7 | 79.1 | 0 | 0 | 1001 | 0.53 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:41 | 28.9 | 1.7 | 19.6 | 49.8 | 0 | 0 | 1001 | 0.26 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:46 | 28.5 | 2.3 | 20 | 49.2 | 0 | 0 | 1001 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:52 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1001 | 0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:04 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1001 | 0.21 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:08 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 1001 | -0.44 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:12 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 1001 | 0.63 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:15 | 0 | 1.8 | 19.5 | 78.7 | 0 | 0 | 1001 | 0.24 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:18 | 0 | 3.1 | 20 | 76.9 | 0 | 0 | 1001 | -0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:21 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 1001 | 0.94 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:28 | 0.2 | 2.6 | 19.4 | 77.8 | 0 | 0 | 1001 | 0.87 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:54 | 0.4 | 2.5 | 19.6 | 77.5 | 0 | 0 | 1001 | -0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:58 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1001 | 0.35 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:01 | 0.3 | 1.5 | 19.8 | 78.4 | 0 | 0 | 1001 | -0.78 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:06 | 0.3 | 2.9 | 19.5 | 77.3 | 0 | 0 | 1001 | 0.63 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:11 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1001 | 0.25 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:14 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1001 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:18 | 0 | 3.4 | 20 | 76.6 | 0 | 0 | 1001 | 0.71 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-10-12
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 9 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 997 | 0.53 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.4 | 0.7 | 19.5 | 79.4 | 0 | 0 | 997 | -0.51 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:52 | 0 | 1.1 | 19.8 | 79.1 | 0 | 0 | 997 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 0.8 | 20 | 79.2 | 0 | 0 | 997 | 0.47 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.6 | 20.2 | 79.2 | 0 | 0 | 997 | 0.57 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 1.1 | 20.1 | 78.8 | 0 | 0 | 997 | 0.53 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 29 | 1.5 | 19.9 | 49.6 | 0 | 0 | 997 | 0.48 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 28.2 | 2.1 | 19.6 | 50.1 | 0 | 0 | 997 | 0.6 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 997 | 0.8 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 997 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.33 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 997 | -0.66 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.4 | 19.7 | 78.9 | 0 | 0 | 997 | 0.39 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 3.4 | 19.9 | 76.7 | 0 | 0 | 997 | 0.41 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 997 | 0.88 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.3 | 2.1 | 19.6 | 78 | 0 | 0 | 997 | 0.46 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.3 | 2.9 | 19.9 | 76.9 | 0 | 0 | 997 | -0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 997 | 0.45 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.4 | 1.6 | 19.9 | 78.1 | 0 | 0 | 997 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.3 | 2.3 | 19.7 | 77.7 | 0 | 0 | 997 | 0.46 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 997 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 997 | -0.66 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 3.2 | 19.9 | 76.9 | 0 | 0 | 997 | 0.41 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-10-19
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 8 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:23 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 997 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:28 | 0.2 | 0.5 | 19.8 | 79.5 | 0 | 0 | 997 | -0.36 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:30 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 997 | -0.78 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:32 | 0 | 0.7 | 19.7 | 79.6 | 0 | 0 | 997 | -0.21 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:35 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 997 | 0.95 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:39 | 0 | 1 | 20 | 79 | 0 | 0 | 997 | -0.63 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:42 | 29.2 | 1.4 | 19.6 | 49.8 | 0 | 0 | 997 | 0.25 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:48 | 27.8 | 2.5 | 19.7 | 50 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:53 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:05 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 997 | -0.65 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:09 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 997 | 0.32 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:13 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 997 | -0.17 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:16 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 997 | 0.36 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:19 | 0 | 3.2 | 19.8 | 77 | 0 | 0 | 997 | -0.98 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:22 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.25 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:29 | 0.2 | 1.8 | 19.5 | 78.5 | 0 | 0 | 997 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:55 | 0.3 | 2.6 | 19.8 | 77.3 | 0 | 0 | 997 | 0.75 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:59 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 997 | 0.36 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:02 | 0.2 | 1.8 | 20 | 78 | 0 | 0 | 997 | -0.82 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:07 | 0.4 | 2.1 | 19.6 | 77.9 | 0 | 0 | 997 | 0.39 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:12 | 0 | 2.5 | 19.7 | 77.8 | 0 | 0 | 997 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:15 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 997 | 0.27 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:19 | 0 | 3.4 | 19.8 | 76.8 | 0 | 0 | 997 | -0.54 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-10-26
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:15 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | 0.42 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:20 | 0.3 | 0.6 | 19.9 | 79.2 | 0 | 0 | 999 | 0.75 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:23 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 999 | 0.12 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:25 | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 999 | 0.29 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:27 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 999 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:31 | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 999 | 0.14 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:34 | 29 | 1.1 | 20 | 49.9 | 0 | 0 | 999 | -0.53 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:40 | 27.9 | 2.6 | 19.2 | 50.3 | 0 | 0 | 999 | 0.26 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:45 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 999 | -0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:57 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 999 | 0.14 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:01 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 999 | -0.77 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:05 | 0 | 2 | 19.8 | 78.2 | 0 | 0 | 999 | 0.56 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:08 | 0 | 1.6 | 19.5 | 78.9 | 0 | 0 | 999 | 0.34 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:11 | 0 | 3 | 19.9 | 77.1 | 0 | 0 | 999 | -0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:14 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 999 | 0.26 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:21 | 0.3 | 1.5 | 20 | 78.2 | 0 | 0 | 999 | 0.31 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:47 | 0.2 | 2.4 | 19.5 | 77.9 | 0 | 0 | 999 | 0.87 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:51 | 0 | 2.4 | 19.2 | 78.4 | 0 | 0 | 999 | 0.9 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:54 | 0.3 | 1.6 | 20 | 78.1 | 0 | 0 | 999 | -0.75 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:59 | 0.4 | 2.4 | 19.5 | 77.7 | 0 | 0 | 999 | -0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:04 | 0 | 2.4 | 19.2 | 78.4 | 0 | 0 | 999 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:07 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 999 | 0.68 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:11 | 0 | 3.5 | 19.5 | 77 | 0 | 0 | 999 | -0.71 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Gas Well Balance Monitoring
Date |  | 2017-10-23
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 9 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:30 | 52.1 | 37.9 | 0.5 | 9.5 | 7 | 10 | 1004 | 165 |  | Engine running 400 KW
GV1 |  | 37 | 23.9 | 1.7 | 37.4 | 9 | 5 | 1004 | -0.21 |  | OFF
GV3 |  | 53.9 | 37.5 | 0.3 | 8.3 | 10 | 6 | 1004 | -27.89 |  | Open Full
GV4 |  | 46.5 | 36.5 | 1.1 | 15.9 | 17 | 8 | 1004 | -5.06 |  | Left Cracked
GV6 |  | 46 | 37.2 | 1.2 | 15.6 | 11 | 9 | 1004 | -5.09 |  | Cracked Open
GV7 |  | 35.9 | 32.8 | 2.7 | 28.6 | 4 | 10 | 1004 | -0.01 |  | Off Low Gas high o2
GV8 |  | 36.7 | 34 | 2.3 | 27 | 7 | 4 | 1004 | -0.04 |  | Off Low Gas high o3
GV9 |  | 52.3 | 37 | 0.1 | 10.6 | 8 | 7 | 1004 | -27.59 |  | Open Full
GV10 |  | 40.9 | 36.5 | 1.3 | 21.3 | 5 | 9 | 1004 | -0.05 |  | Off
GV11 |  | 47.2 | 36.9 | 1.1 | 14.8 | 10 | 8 | 1004 | 8.71 | 5.02 | Regulated
GV12+R3 Manifold |  | 51.2 | 37.8 | 0.5 | 10.5 | 6 | 6 | 1004 | -27.56 |  | Open Full
GV12 |  | 51.9 | 38.2 | 0.2 | 9.7 | 3 | 8 | 1004 | -27.69 |  | Open Full
R3 |  | 50.5 | 36.9 | 0.6 | 12 | 9 | 4 | 1004 | -27.36 |  | Open Full
GV13 |  | 2.5 | 4.9 | 20.1 | 72.5 | 10 | 10 | 1004 | 0.01 |  | Left Closed
GV14 |  | 51.1 | 36.9 | 0.3 | 11.7 | 6 | 9 | 1004 | -27.74 |  | Open Full
GV15 |  | 52.9 | 37 | 0.5 | 9.6 | 8 | 5 | 1004 | -27.56 |  | Open Full
GV16 |  | 37.5 | 38.2 | 1.3 | 23 | 5 | 6 | 1004 | 0.02 |  | Left Closed
GV17+LC4 Manifold |  | 48 | 36.2 | 2.4 | 13.4 | 5 | 8 | 1004 | -0.05 |  | Off at Manifold Gas drops quick.
GV17 |  | 46.3 | 38.3 | 2.2 | 13.2 | 4 | 7 | 1004 | -0.04 |  | Open Full at Well
LC4 |  | 49 | 35.9 | 3.2 | 11.9 | 7 | 10 | 1004 | -0.09 |  | Open Full at well
GV18 |  | 50.8 | 36.2 | 0.3 | 12.7 | 9 | 8 | 1004 | -27.48 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 47.5 | 35.2 | 1.6 | 15.7 | 10 | 7 | 1004 | -0.01 |  | Off gas drops off quick.
GV23 |  | 50.5 | 36.2 | 0.3 | 13 | 8 | 8 | 1004 | -27.59 |  | Open Full
GV24 |  | 51.2 | 36.9 | 0.5 | 11.4 | 6 | 6 | 1004 | -27.32 |  | Open Full
GV25 |  | 43.6 | 36 | 1.5 | 18.9 | 9 | 3 | 1004 | -0.27 |  | Left Closed
GV26 + 27 Manifold |  | 52.2 | 36.7 | 0.5 | 10.6 | 10 | 11 | 1004 | -27.59 |  | Open Full
GV28+ 29 Manifold |  | 51.8 | 36.6 | 0.4 | 11.2 | 3 | 7 | 1004 | -27.49 |  | Open Full
GV26 |  | 52.6 | 36.2 | 0.3 | 10.9 | 6 | 12 | 1004 | -27.65 |  | Open Full
GV27 |  | 51.9 | 37.5 | 0.6 | 10 | 12 | 6 | 1004 | -27.42 |  | Open Full
GV28 |  | 52.3 | 36 | 0.2 | 11.5 | 2 | 3 | 1004 | -27.55 |  | Open Full
GV29 |  | 50 | 37.5 | 0.6 | 11.9 | 4 | 8 | 1004 | -27.43 |  | Open Full
GVA |  | 36.9 | 31.2 | 2.5 | 29.4 | 4 | 5 | 1004 | 0 |  | Off Low gas
B+C Manifold |  | 50.5 | 36.8 | 0.6 | 12.1 | 10 | 8 | 1004 | -27.36 |  | Open Full
GV B |  | 51 | 37.2 | 0.7 | 11.1 | 6 | 10 | 1004 | -27.21 |  | Open Full
GV C |  | 49.8 | 36.5 | 0.4 | 13.3 | 14 | 7 | 1004 | -27.48 |  | Open Full
GV30 |  | 48.5 | 36.4 | 1.1 | 14 | 10 | 10 | 1004 | 14.99 | 12.06 | cracked open
GV31 |  | 48.8 | 36.9 | 1 | 13.3 | 4 | 7 | 1004 | -11.09 |  | Cracked Open
GV32 |  | 48.9 | 36.9 | 1 | 13.2 | 6 | 8 | 1004 | 13.58 | 15.24 | Cracked Open
GV33 |  | 49.5 | 37 | 1 | 12.5 | 3 | 10 | 1004 | -11 | -12.57 | Cracked Open
GV34 |  | 47 | 36.2 | 1.1 | 15.7 | 8 | 11 | 1004 | -6.32 |  | Cracked Open
GV 35 (New Well) |  | 25.4 | 29.9 | 1.8 | 42.9 | 2 | 4 | 1004 | -0.28 |  | Left Closed
GV 36 (New Well) |  | 33.9 | 31.4 | 5 | 29.7 | 10 | 6 | 1004 | -0.04 |  | OFF low gas.
GV 37 (New Well) |  | 38.7 | 36.9 | 2.1 | 22.3 | 9 | 3 | 1004 | -0.02 |  | closed hign o2 low gas
GV 38 (New Well) |  | 46.2 | 36.1 | 1.1 | 16.6 | 6 | 2 | 1004 | -7.48 |  | Cracked Open
GV 39 (New Well) |  | 46.5 | 36.5 | 1 | 16 | 7 | 5 | 1004 | -7.69 |  | Cracked Open
GV 40 (New Well) |  | 46 | 37 | 1.2 | 15.8 | 11 | 5 | 1004 | -7.41 |  | Cracked Open
GV 41 (New Well) |  | 46.9 | 36.5 | 1.1 | 15.5 | 15 | 8 | 1004 | -7.02 |  | Cracked Open
GV 42 (New Well) |  | 37.5 | 36.2 | 1.9 | 24.4 | 9 | 4 | 1004 | -0.06 |  | Off Low Gas
GV 43 (New Well) |  | 47.5 | 37 | 1.2 | 14.3 | 6 | 6 | 1004 | -7.23 |  | Cracked open
GV 44 (New Well) |  | 41.3 | 37 | 1.4 | 20.3 | 5 | 5 | 1004 | -0.35 |  | Off Low gas
GV 45 (New Well) |  | 46.5 | 36 | 1 | 16.5 | 7 | 6 | 1004 | -6.34 |  | Cracked Open
GV 46 (New Well) |  | 50.8 | 37.5 | 0.3 | 11.4 | 5 | 9 | 1004 | -27.59 |  | Open Full
GV 47 (New Well) |  | 48.2 | 37 | 1.1 | 13.7 | 7 | 10 | 1004 | -6.99 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 7 | 4 | 1004 | -27.81 |  | Open Full
GV 49 (New Well) |  | 42.8 | 36.9 | 2 | 18.3 | 4 | 7 | 1004 | -0.08 |  | Left Closed
LC1B |  | 34.8 | 36 | 2.9 | 26.3 | 8 | 8 | 1004 | -0.58 |  | OFF
LC2R? |  | 53.6 | 37.8 | 0.1 | 8.5 | 5 | 6 | 1004 | -27.11 |  | Open Full
GV 2.1 |  | 55.4 | 36 | 0.1 | 8.5 | 10 | 6 | 1004 | -27.49 |  | Open Full
GV 2.2+ LC2B MAN |  | 38 | 32.5 | 6.4 | 23.1 | 11 | 6 | 1004 | -0.05 |  | Left Closed
GV 2.2 |  | 40 | 31.5 | 4.5 | 24 | 14 | 5 | 1004 | -0.08 |  | Left Closed
LC2B |  | 36.5 | 32.9 | 7.2 | 23.4 | 9 | 8 | 1004 | -0.02 |  | Left Closed
GV / LC3.1 + LC3 MAN |  | 49 | 37.2 | 1 | 12.8 | 10 | 5 | 1004 | -10.99 |  | Left Open Half Way
LC3.1 |  | 49 | 37.2 | 1 | 12.8 | 10 | 5 | 1004 | -10.99 |  | Left open half way
LC3 |  | 43 | 37 | 2.5 | 17.5 | 6 | 5 | 1004 | -0.05 |  | OFF
LC4B |  | 49 | 37.2 | 1.1 | 12.7 | 11 | 7 | 1004 | -7.59 |  | Left Cracked Open
R1 + R1B Manifold |  | 53.6 | 37.5 | 0.9 | 8 | 10 | 8 | 1004 | -27.89 |  | Open Full
R1 |  | 49 | 36.8 | 1.2 | 13 | 8 | 5 | 1004 | -8.02 |  | Cracked Open
R1B |  | 54.2 | 38.5 | 0.5 | 6.8 | 13 | 10 | 1004 | -27.84 |  | Open Full
R2B |  | 53.6 | 36.9 | 0.2 | 9.3 | 12 | 10 | 1004 | -27.46 |  | Open Full
R4B |  | 44.5 | 37.5 | 2.7 | 15.3 | 8 | 6 | 1004 | 0.07 |  | Left closed
R6B |  | 55 | 37.9 | 0.2 | 6.9 | 1 | 2 | 1004 | -27.04 |  | Open Full
LC5 |  | 47 | 35.4 | 2.6 | 15 | 0 | 3 | 1004 | -0.35 |  | Left Off ( Gas drops quick)
LC6 |  | 47.2 | 33.5 | 2.9 | 16.4 | 3 | 1 | 1004 | -0.17 |  | Left Off ( Gas drops quick)
LC6B |  | 51.2 | 37 | 0.3 | 11.5 | 2 | 4 | 1004 | -27.93 |  | Open Full
PW1 |  | 3 | 1.8 | 8 | 87.2 | 4 | 2 | 1004 | -0.04 |  | Left Off
PW2 |  | 32.5 | 19 | 2.5 | 46 | 1 | 0 | 1004 | -0.58 |  | Left Off
PW3 |  | 34.9 | 19.9 | 3.4 | 41.8 | 3 | 7 | 1004 | -0.29 |  | Left Off
PW4 |  | 47.2 | 34.5 | 1.2 | 17.1 | 2 | 8 | 1004 | -5.41 |  | Cracked Open
PW5 |  | 38 | 26 | 1.9 | 34.1 | 6 | 10 | 1004 | -0.38 |  | Left Off
PW6 |  | 37.9 | 28 | 3.5 | 30.6 | 5 | 7 | 1004 | -0.47 |  | Left Off
Flare | 14:00 | 52.2 | 37.9 | 0.4 | 9.5 | 7 | 11 | 1004 | 165 |  | Engine running 400 KW. Flow 425m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## Nov 2017
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-11-02
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:46 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1001 | 0.72 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:51 | 0.2 | 0.5 | 19.8 | 79.5 | 0 | 0 | 1001 | -0.57 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:53 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1001 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:55 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1001 | 0.59 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:58 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 1001 | 0.77 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:02 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 1001 | 0.9 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:05 | 28.6 | 1 | 19.9 | 50.5 | 0 | 0 | 1001 | 0.67 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:11 | 28 | 2.3 | 19.8 | 49.9 | 0 | 0 | 1001 | 0.69 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:16 | 0 | 1.7 | 19.6 | 78.7 | 0 | 0 | 1001 | 0.74 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:28 | 0 | 2.5 | 19.5 | 78 | 0 | 0 | 1001 | -0.56 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:32 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1001 | 0.41 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:36 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1001 | -0.87 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:39 | 0 | 1.7 | 20.1 | 78.2 | 0 | 0 | 1001 | 0.37 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:42 | 0 | 3.5 | 19.7 | 76.8 | 0 | 0 | 1001 | 0.52 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:45 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1001 | 1.19 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:52 | 0.2 | 1.4 | 19.5 | 78.9 | 0 | 0 | 1001 | 0.91 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:18 | 0.3 | 2.6 | 19.6 | 77.5 | 0 | 0 | 1001 | 0.67 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:22 | 0 | 2.2 | 19.9 | 77.9 | 0 | 0 | 1001 | 0.83 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:25 | 0.2 | 1.9 | 19.8 | 78.1 | 0 | 0 | 1001 | 0.46 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:30 | 0.2 | 2 | 20 | 77.8 | 0 | 0 | 1001 | 0.58 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:35 | 0 | 2.1 | 19.3 | 78.6 | 0 | 0 | 1001 | 0.93 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:38 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 1001 | -0.67 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:42 | 0 | 3.6 | 19.9 | 76.5 | 0 | 0 | 1001 | 0.63 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-11-09
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 997 | -0.52 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.3 | 0.6 | 19.5 | 79.6 | 0 | 0 | 997 | -0.12 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:10 | 0 | 1.4 | 19.8 | 78.8 | 0 | 0 | 997 | -0.64 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:12 | 0 | 0.7 | 20 | 79.3 | 0 | 0 | 997 | -0.58 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 997 | 0.77 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:19 | 0 | 1.3 | 19.8 | 78.9 | 0 | 0 | 997 | 0.52 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 28.7 | 1.6 | 19.7 | 50 | 0 | 0 | 997 | 0.46 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.8 | 2.4 | 20 | 48.8 | 0 | 0 | 997 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.5 | 19.3 | 79.2 | 0 | 0 | 997 | 0.36 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 997 | -0.25 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 997 | -0.11 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 997 | 0.69 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.8 | 19.9 | 78.3 | 0 | 0 | 997 | 0.75 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 3.2 | 20 | 76.8 | 0 | 0 | 997 | -0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 997 | 0.29 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 1.3 | 19.8 | 78.6 | 0 | 0 | 997 | -0.26 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.2 | 2.4 | 19.9 | 77.5 | 0 | 0 | 997 | 0.52 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 2 | 19.6 | 78.4 | 0 | 0 | 997 | 0.46 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:42 | 0.4 | 1.5 | 19.7 | 78.4 | 0 | 0 | 997 | -0.68 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.3 | 2.3 | 19.8 | 77.6 | 0 | 0 | 997 | -0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 997 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 997 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 3.9 | 20 | 76.1 | 0 | 0 | 997 | 0.38 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-11-16
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 7 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:27 | 0 | 1.9 | 20 | 78.1 | 0 | 0 | 1005 | -0.35 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:32 | 0.2 | 0.8 | 19.9 | 79.1 | 0 | 0 | 1005 | 0.76 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:34 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1005 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:36 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1005 | -0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:39 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1005 | 0.52 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:43 | 0 | 1.6 | 19.4 | 79 | 0 | 0 | 1005 | 0.48 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:46 | 29 | 1.5 | 19.8 | 49.7 | 0 | 0 | 1005 | -0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:52 | 28.6 | 2.3 | 19.9 | 49.2 | 0 | 0 | 1005 | 0.36 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:57 | 0 | 1.7 | 20 | 78.3 | 0 | 0 | 1005 | -0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:09 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 1005 | 0.16 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:13 | 0 | 2.6 | 19.7 | 77.7 | 0 | 0 | 1005 | 0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:17 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1005 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:20 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1005 | 0.35 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:23 | 0 | 3.1 | 20.1 | 76.8 | 0 | 0 | 1005 | -0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:26 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1005 | 0.48 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:33 | 0.2 | 1.1 | 19.8 | 78.9 | 0 | 0 | 1005 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:59 | 0.2 | 2.9 | 19.7 | 77.2 | 0 | 0 | 1005 | 0.25 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:03 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 1005 | 0.69 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:06 | 0.2 | 1.7 | 19.9 | 78.2 | 0 | 0 | 1005 | -0.17 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:11 | 0.4 | 2.4 | 19.9 | 77.3 | 0 | 0 | 1005 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:16 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1005 | 0.39 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:19 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 1005 | -0.42 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:23 | 0 | 3.5 | 19.8 | 76.7 | 0 | 0 | 1005 | 0.28 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-11-23
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GEM 2000
Serial No: | GM12289
Calibrated To: | 29/11//2017
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:07 | 0 | 2 | 19.9 | 78.1 | 0 | 0 | 1003 | -0.54 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0.3 | 0.9 | 19.8 | 79 | 0 | 0 | 1003 | 0.32 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:11 | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 1003 | -0.32 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:14 | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1003 | 0.28 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:16 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1003 | 0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:20 | 0 | 1.4 | 19.4 | 79.2 | 0 | 0 | 1003 | -0.65 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 29.5 | 1.6 | 19.7 | 49.2 | 0 | 0 | 1003 | 0.34 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 28.9 | 2.1 | 19.6 | 49.4 | 0 | 0 | 1003 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.6 | 19.8 | 78.6 | 0 | 0 | 1003 | 0.25 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:46 | 0 | 3 | 19.9 | 77.1 | 0 | 0 | 1003 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 1003 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 2.4 | 19.9 | 77.7 | 0 | 0 | 1003 | 0.69 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 1003 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:00 | 0 | 3.5 | 19.8 | 76.7 | 0 | 0 | 1003 | 0.23 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1003 | -0.42 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.3 | 1.4 | 19.9 | 78.4 | 0 | 0 | 1003 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0.4 | 2.5 | 19.9 | 77.2 | 0 | 0 | 1003 | -0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:37 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1003 | -0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:40 | 0.3 | 1.8 | 20 | 77.9 | 0 | 0 | 1003 | 0.6 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0.2 | 2.1 | 19.8 | 77.9 | 0 | 0 | 1003 | 0.27 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 2.8 | 19.5 | 77.7 | 0 | 0 | 1003 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:54 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1003 | 0.25 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:02 | 0 | 3.4 | 19.7 | 76.9 | 0 | 0 | 1003 | -0.58 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2017-11-30
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:38 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1002 | -0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:43 | 0.4 | 0.8 | 19.8 | 79 | 0 | 0 | 1002 | 0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:44 | 0 | 1.1 | 19.9 | 79 | 0 | 0 | 1002 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:47 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 1002 | 0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:50 | 0 | 0.7 | 19.5 | 79.8 | 0 | 0 | 1002 | -0.56 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:54 | 0 | 1.6 | 19.9 | 78.5 | 0 | 0 | 1002 | 0.24 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:57 | 29.4 | 1.5 | 19.7 | 49.4 | 0 | 0 | 1002 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:03 | 28.7 | 2 | 19.9 | 49.4 | 0 | 0 | 1002 | -0.28 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:08 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1002 | -0.63 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:20 | 0 | 2.6 | 19.8 | 77.6 | 0 | 0 | 1002 | 0.11 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:24 | 0 | 2.7 | 19.9 | 77.4 | 0 | 0 | 1002 | 0.78 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:28 | 0 | 2.6 | 19.4 | 78 | 0 | 0 | 1002 | -0.15 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:31 | 0 | 1.5 | 19.8 | 78.7 | 0 | 0 | 1002 | 0.21 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:34 | 0 | 3.1 | 20 | 76.9 | 0 | 0 | 1002 | -0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:37 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1002 | 0.21 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:44 | 0.2 | 1.5 | 19.9 | 78.4 | 0 | 0 | 1002 | -0.75 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:10 | 0.3 | 2.6 | 19.6 | 77.5 | 0 | 0 | 1002 | -0.63 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:14 | 0 | 2.1 | 19.5 | 78.4 | 0 | 0 | 1002 | 0.54 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:17 | 0.4 | 1.9 | 19.9 | 77.8 | 0 | 0 | 1002 | -0.96 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:22 | 0.3 | 2.4 | 19.9 | 77.4 | 0 | 0 | 1002 | -0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:27 | 0 | 2.5 | 19.8 | 77.7 | 0 | 0 | 1002 | 0.34 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:30 | 0 | 0.7 | 19.3 | 80 | 0 | 0 | 1002 | -0.44 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:34 | 0 | 3.5 | 19.7 | 76.8 | 0 | 0 | 1002 | 0.25 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## Dec 2017
Date | 2017-12-07
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 4 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:15 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 997 | -0.5 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:20 | 0.3 | 0.9 | 19.8 | 79 | 0 | 0 | 997 | 0.71 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:22 | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 997 | 0.62 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:24 | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 997 | 0.54 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:27 | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 997 | 0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:31 | 0 | 2 | 20 | 78 | 0 | 0 | 997 | -0.15 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:34 | 29.2 | 1.9 | 19.6 | 49.3 | 0 | 0 | 997 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:40 | 28.9 | 1.9 | 19.2 | 50 | 0 | 0 | 997 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:45 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 997 | 0.75 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:57 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 997 | 0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:01 | 0 | 2.9 | 20 | 77.1 | 0 | 0 | 997 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:05 | 0 | 2.2 | 19.8 | 78 | 0 | 0 | 997 | 0.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:08 | 0 | 1.7 | 19.7 | 78.6 | 0 | 0 | 997 | 0.46 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:11 | 0 | 3 | 19.6 | 77.4 | 0 | 0 | 997 | -0.14 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:14 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 997 | 0.69 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:21 | 0.3 | 1.9 | 19.9 | 77.9 | 0 | 0 | 997 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:47 | 0.2 | 2.4 | 20 | 77.4 | 0 | 0 | 997 | -0.47 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:51 | 0 | 2.4 | 19.6 | 78 | 0 | 0 | 997 | -0.15 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:54 | 0.3 | 2.1 | 19.8 | 77.8 | 0 | 0 | 997 | 0.63 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:59 | 0.2 | 2.6 | 20 | 77.2 | 0 | 0 | 997 | -0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:04 | 0 | 2.4 | 19.5 | 78.1 | 0 | 0 | 997 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:07 | 0 | 0.8 | 19.9 | 79.3 | 0 | 0 | 997 | 0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:11 | 0 | 3.4 | 20 | 76.6 | 0 | 0 | 997 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-12-14
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 6 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:38 | 0 | 2.4 | 20 | 77.6 | 0 | 0 | 1008 | 0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:43 | 0.2 | 0.8 | 19.6 | 79.4 | 0 | 0 | 1008 | -0.66 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:45 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1008 | 0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:47 | 0 | 0.8 | 19.8 | 79.4 | 0 | 0 | 1008 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:50 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 1008 | 0.65 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:54 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1008 | 0.45 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:57 | 30 | 1.5 | 19.9 | 48.6 | 0 | 0 | 1008 | -0.26 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 12:03 | 29.1 | 1.8 | 19.8 | 49.3 | 0 | 0 | 1008 | 0.55 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 12:08 | 0 | 1 | 19.9 | 79.1 | 0 | 0 | 1008 | 0.77 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:20 | 0 | 2.8 | 20 | 77.2 | 0 | 0 | 1008 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:24 | 0 | 2 | 20 | 78 | 0 | 0 | 1008 | 0.29 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:28 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1008 | -0.67 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:31 | 0 | 1.9 | 19.8 | 78.3 | 0 | 0 | 1008 | 0.33 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:34 | 0 | 3.2 | 19.3 | 77.5 | 0 | 0 | 1008 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:37 | 0 | 2.3 | 19.1 | 78.6 | 0 | 0 | 1008 | 0.68 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:44 | 0.2 | 1.4 | 19.8 | 78.6 | 0 | 0 | 1008 | 0.47 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:10 | 0.4 | 2.1 | 19.7 | 77.8 | 0 | 0 | 1008 | -0.45 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:14 | 0 | 3 | 19.9 | 77.1 | 0 | 0 | 1008 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:17 | 0.4 | 2.5 | 19.6 | 77.5 | 0 | 0 | 1008 | 0.03 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:22 | 0.3 | 2.9 | 19.8 | 77 | 0 | 0 | 1008 | 0.18 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 11:27 | 0 | 2.1 | 19.9 | 78 | 0 | 0 | 1008 | 0.43 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 11:30 | 0 | 0.9 | 19.7 | 79.4 | 0 | 0 | 1008 | -0.5 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:34 | 0 | 3.2 | 20 | 76.8 | 0 | 0 | 1008 | 0.42 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-12-21
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 2 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:19 | 0 | 2.5 | 19.9 | 77.6 | 0 | 0 | 1000 | 0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:24 | 0.3 | 0.6 | 19.5 | 79.6 | 0 | 0 | 1000 | -0.63 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:25 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1000 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:27 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 1000 | 0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:31 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1000 | 0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:35 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1000 | 0.44 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:38 | 29.5 | 1.2 | 19.7 | 49.6 | 0 | 0 | 1000 | -0.37 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:44 | 28.6 | 1.5 | 19.9 | 50 | 0 | 0 | 1000 | 0.68 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:49 | 0 | 1.8 | 20 | 78.2 | 0 | 0 | 1000 | 0.78 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:01 | 0 | 2.1 | 19.6 | 78.3 | 0 | 0 | 1000 | -0.23 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:05 | 0 | 2.5 | 19.3 | 78.2 | 0 | 0 | 1000 | 0.39 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:09 | 0 | 3 | 19.8 | 77.2 | 0 | 0 | 1000 | -0.74 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:12 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1000 | 0.48 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:15 | 0 | 2.6 | 20 | 77.4 | 0 | 0 | 1000 | 0.26 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:18 | 0 | 3.9 | 19.6 | 76.5 | 0 | 0 | 1000 | 0.7 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:25 | 0.3 | 1.2 | 19.8 | 78.7 | 0 | 0 | 1000 | 0.49 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:51 | 0.3 | 2.1 | 19.2 | 78.4 | 0 | 0 | 1000 | -0.23 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:55 | 0 | 2.5 | 19.7 | 77.8 | 0 | 0 | 1000 | 0.37 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 9:58 | 0.4 | 3.9 | 19.9 | 75.8 | 0 | 0 | 1000 | 0.21 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:03 | 0.4 | 2.1 | 20 | 77.5 | 0 | 0 | 1000 | 0.2 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:08 | 0 | 2.6 | 19.3 | 78.1 | 0 | 0 | 1000 | 0.67 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:11 | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1000 | -0.55 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:15 | 0 | 3.3 | 19.8 | 76.9 | 0 | 0 | 1000 | 0.67 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2017-12-28
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:00 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1005 | 0.69 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:05 | 0.4 | 0.8 | 19.7 | 79.1 | 0 | 0 | 1005 | -0.48 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 11:07 | 0 | 2 | 19.5 | 78.5 | 0 | 0 | 1005 | 0.24 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:10 | 0 | 0.7 | 19.3 | 80 | 0 | 0 | 1005 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:13 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 1005 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:16 | 0 | 2.3 | 19.8 | 77.9 | 0 | 0 | 1005 | 0.87 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:19 | 29 | 1.5 | 19.3 | 50.2 | 0 | 0 | 1005 | 0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:25 | 28.4 | 1.8 | 19.9 | 49.9 | 0 | 0 | 1005 | 0.78 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:30 | 0 | 1.5 | 20 | 78.5 | 0 | 0 | 1005 | 0.71 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:42 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1005 | -0.62 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:46 | 0 | 2.9 | 19.8 | 77.3 | 0 | 0 | 1005 | 0.47 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:50 | 0 | 2.8 | 19.7 | 77.5 | 0 | 0 | 1005 | -0.97 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:53 | 0 | 1.2 | 19.5 | 79.3 | 0 | 0 | 1005 | 0.48 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:56 | 0 | 2.8 | 19.3 | 77.9 | 0 | 0 | 1005 | 0.56 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:59 | 0 | 3.8 | 19.8 | 76.4 | 0 | 0 | 1005 | 1.27 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:06 | 0.2 | 1.1 | 19.5 | 79.2 | 0 | 0 | 1005 | 0.89 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:33 | 0.4 | 2.6 | 19.8 | 77.2 | 0 | 0 | 1005 | 0.59 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:36 | 0 | 2.9 | 19.6 | 77.5 | 0 | 0 | 1005 | 0.74 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 10:39 | 0.3 | 3.5 | 20 | 76.2 | 0 | 0 | 1005 | 0.5 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:44 | 0.2 | 2.7 | 19.9 | 77.2 | 0 | 0 | 1005 | 0.56 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:49 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1005 | 0.85 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:52 | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1005 | -0.89 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:56 | 0 | 3.5 | 19.8 | 76.7 | 0 | 0 | 1005 | 0.62 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date |  | 2017-12-20
Weather: |  | Cloudy
Wind conditions: |  | Breezy
Air Temperature: |  | 4 | oC
Instrument: |  | GEM 2000 | (with H2s filter fitted)
Serial No: |  | GM12289
Calibrated To: |  | 2017-11-29
Operative
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Rel Pressure | Comments
Point | Hrs | % | % | % | % | ppm | ppm | mb | Before Reg | After Reg
Flare | 10:30 | 54.2 | 38.8 | 0.4 | 6.6 | 5 | 9 | 1006 | 170 |  | Engine running 400 KW
GV1 |  | 37 | 25.5 | 1.3 | 36.2 | 6 | 5 | 1006 | -0.21 |  | OFF
GV3 |  | 53.9 | 38 | 0.3 | 7.8 | 2 | 1 | 1006 | -28.45 |  | Open Full
GV4 |  | 46.9 | 36.3 | 1.1 | 15.7 | 10 | 6 | 1006 | -6.02 |  | Left Cracked
GV6 |  | 47 | 36.1 | 1.2 | 15.7 | 8 | 3 | 1006 | -6.32 |  | Cracked Open
GV7 |  | 35.6 | 34.1 | 2.6 | 27.7 | 9 | 8 | 1006 | -0.01 |  | Off Low Gas high o2
GV8 |  | 33.1 | 35 | 3.5 | 28.4 | 2 | 7 | 1006 | -0.06 |  | Off Low Gas high o3
GV9 |  | 53.9 | 38 | 0.3 | 7.8 | 6 | 9 | 1006 | -28.96 |  | Open Full
GV10 |  | 42 | 36.5 | 1.6 | 19.9 | 4 | 2 | 1006 | -0.05 |  | Off
GV11 |  | 47.5 | 36.2 | 1.9 | 14.4 | 8 | 5 | 1006 | -0.02 |  | Left Closed
GV12+R3 Manifold |  | 52.8 | 38.1 | 0.3 | 8.8 | 5 | 6 | 1006 | -28.14 |  | Open Full
GV12 |  | 54 | 38.6 | 0.2 | 7.2 | 2 | 4 | 1006 | -27.99 |  | Open Full
R3 |  | 51.5 | 37.5 | 0.4 | 10.6 | 6 | 8 | 1006 | -28.59 |  | Open Full
GV13 |  | 2.9 | 4.9 | 18.5 | 73.7 | 7 | 10 | 1006 | -0.01 |  | Left Closed
GV14 |  | 52.4 | 36.9 | 0.3 | 10.4 | 9 | 14 | 1006 | -28.55 |  | Open Full
GV15 |  | 52.3 | 36.4 | 0.2 | 11.1 | 11 | 8 | 1006 | -28.37 |  | Open Full
GV16 |  | 37.4 | 35.8 | 1.9 | 24.9 | 10 | 3 | 1006 | 0.01 |  | Left Closed
GV17+LC4 Manifold |  | 48.5 | 36.4 | 2.9 | 12.2 | 6 | 2 | 1006 | -0.08 |  | Off at Manifold Gas drops quick.
GV17 |  | 46.9 | 38.5 | 1.9 | 12.7 | 5 | 6 | 1006 | -0.03 |  | Open Full at Well
LC4 |  | 49 | 36 | 3.5 | 11.5 | 10 | 1 | 1006 | -0.1 |  | Open Full at well
GV18 |  | 51.6 | 36 | 0.3 | 12.1 | 12 | 4 | 1006 | -28.36 |  | Left open Full
Point: GV19 |  |  | N/A Going to decommission.
GV 22 |  | 47.2 | 36 | 1.6 | 15.2 | 1 | 3 | 1006 | -0.04 |  | Off gas drops off quick.
GV23 |  | 51.8 | 37 | 0.3 | 10.9 | 9 | 6 | 1006 | -28.56 |  | Open Full
GV24 |  | 52.3 | 36.9 | 0.3 | 10.5 | 6 | 5 | 1006 | -28.71 |  | Open Full
GV25 |  | 43.2 | 35.8 | 1.5 | 19.5 | 3 | 10 | 1006 | -0.28 |  | Left Closed
GV26 + 27 Manifold |  | 52.9 | 36.5 | 0.3 | 10.3 | 8 | 14 | 1006 | -28.51 |  | Open Full
GV28+ 29 Manifold |  | 52.6 | 37 | 0.4 | 10 | 10 | 1 | 1006 | -28.49 |  | Open Full
GV26 |  | 53.4 | 36 | 0.3 | 10.3 | 4 | 8 | 1006 | -28.69 |  | Open Full
GV27 |  | 52 | 37.5 | 0.6 | 9.9 | 10 | 16 | 1006 | -28.41 |  | Open Full
GV28 |  | 53.9 | 36.8 | 0.3 | 9 | 12 | 0 | 1006 | -28.38 |  | Open Full
GV29 |  | 51.4 | 37.6 | 0.6 | 10.4 | 4 | 5 | 1006 | -28.84 |  | Open Full
GVA |  | 36.9 | 33.9 | 2.2 | 27 | 6 | 7 | 1006 | 0 |  | Off Low gas
B+C Manifold |  | 51.4 | 36.9 | 0.6 | 11.1 | 12 | 10 | 1006 | -28.32 |  | Open Full
GV B |  | 52 | 37.1 | 0.7 | 10.2 | 17 | 11 | 1006 | -28.16 |  | Open Full
GV C |  | 50.5 | 36.4 | 0.3 | 12.8 | 8 | 3 | 1006 | -28.6 |  | Open Full
GV30 |  | 47.9 | 36.4 | 1.2 | 14.5 | 6 | 5 | 1006 | -11.32 |  | cracked open
GV31 |  | 48.5 | 36.5 | 1.2 | 13.8 | 5 | 9 | 1006 | -10.99 |  | Cracked Open
GV32 |  | 47.6 | 37.5 | 1.1 | 13.8 | 6 | 5 | 1006 | -14.51 |  | Cracked Open
GV33 |  | 47.8 | 36.9 | 1.1 | 14.2 | 9 | 1 | 1006 | -13.29 |  | Cracked Open
GV34 |  | 46.9 | 36.5 | 1.2 | 15.4 | 10 | 1 | 1006 | -6.03 |  | Cracked Open
GV 35 (New Well) |  | 27.9 | 32.8 | 2.3 | 37 | 3 | 5 | 1006 | -0.05 |  | Left Closed
GV 36 (New Well) |  | 33.9 | 33.4 | 5.2 | 27.5 | 8 | 11 | 1006 | -0.07 |  | OFF low gas.
GV 37 (New Well) |  | 36.9 | 35.9 | 2.2 | 25 | 10 | 8 | 1006 | -0.01 |  | closed hign o2 low gas
GV 38 (New Well) |  | 47 | 36.1 | 1.1 | 15.8 | 4 | 3 | 1006 | -8.06 |  | Cracked Open
GV 39 (New Well) |  | 46.5 | 36.5 | 1.1 | 15.9 | 9 | 2 | 1006 | -7.11 |  | Cracked Open
GV 40 (New Well) |  | 46.5 | 36.5 | 1.2 | 15.8 | 7 | 9 | 1006 | -7.45 |  | Cracked Open
GV 41 (New Well) |  | 47.1 | 37 | 1.1 | 14.8 | 10 | 2 | 1006 | -7.98 |  | Cracked Open
GV 42 (New Well) |  | 37 | 35.8 | 1.9 | 25.3 | 12 | 8 | 1006 | -0.08 |  | Off Low Gas
GV 43 (New Well) |  | 47.6 | 37.1 | 1.2 | 14.1 | 13 | 1 | 1006 | -8 |  | Cracked open
GV 44 (New Well) |  | 43 | 36.9 | 2.3 | 17.8 | 10 | 4 | 1006 | -0.32 |  | Off Low gas
GV 45 (New Well) |  | 46.2 | 36.5 | 1.1 | 16.2 | 7 | 5 | 1006 | -7.17 |  | Cracked Open
GV 46 (New Well) |  | 52.4 | 37 | 0.3 | 10.3 | 9 | 7 | 1006 | -28.98 |  | Open Full
GV 47 (New Well) |  | 48 | 37.5 | 1.2 | 13.3 | 10 | 5 | 1006 | -6.84 |  | Cracked Opem
GV 48 (New Well) |  | 60 | 40 | 0 | 0 | 11 | 4 | 1006 | -28.94 |  | Open Full
GV 49 (New Well) |  | 44.1 | 36.4 | 2.6 | 16.9 | 4 | 1 | 1006 | -0.05 |  | Left Closed
LC1B |  | 36.9 | 35.8 | 2.9 | 24.4 | 7 | 3 | 1006 | -0.52 |  | OFF
LC2R? |  | 54.8 | 37.2 | 0.1 | 7.9 | 6 | 2 | 1006 | -28.59 |  | Open Full
GV 2.1 |  | 55.3 | 36.9 | 0.2 | 7.6 | 3 | 8 | 1006 | -28.41 |  | Open Full
GV 2.2+ LC2B MAN |  | 38 | 34.2 | 4.9 | 22.9 | 5 | 6 | 1006 | -0.04 |  | Left Closed
GV 2.2 |  | 41.2 | 32.4 | 4.5 | 21.9 | 5 | 7 | 1006 | -0.07 |  | Left Closed
LC2B |  | 37.8 | 36.5 | 6.2 | 19.5 | 6 | 1 | 1006 | -0.02 |  | Left Closed
GV / LC3.1 + LC3 MAN |  | 50.1 | 34.9 | 1.1 | 13.9 | 11 | 9 | 1006 | -11.52 |  | Left Open Half Way
LC3.1 |  | 50.1 | 34.9 | 1.1 | 13.9 | 11 | 9 | 1006 | -11.52 |  | Left open half way
LC3 |  | 44.6 | 36.9 | 2.5 | 16 | 8 | 8 | 1006 | -0.08 |  | OFF
LC4B |  | 48.9 | 37 | 1.1 | 13 | 9 | 7 | 1006 | -7.12 |  | Left Cracked Open
R1 + R1B Manifold |  | 53.2 | 36.8 | 0.8 | 9.2 | 10 | 10 | 1006 | -28.51 |  | Open Full
R1 |  | 48.6 | 36.5 | 1.2 | 13.7 | 4 | 8 | 1006 | -10.11 |  | Cracked Open
R1B |  | 53.8 | 37.9 | 0.5 | 7.8 | 12 | 13 | 1006 | -28.96 |  | Open Full
R2B |  | 52.4 | 36.9 | 0.4 | 10.3 | 10 | 10 | 1006 | -28.03 |  | Open Full
R4B |  | 45.8 | 37 | 2.6 | 14.6 | 2 | 5 | 1006 | -0.02 |  | Left closed
R6B |  | 53.9 | 36.8 | 0.4 | 8.9 | 9 | 8 | 1006 | -28.54 |  | Open Full
LC5 |  | 47 | 35.7 | 2.2 | 15.1 | 10 | 9 | 1006 | -0.26 |  | Left Off ( Gas drops quick)
LC6 |  | 46.8 | 35.9 | 3.2 | 14.1 | 3 | 10 | 1006 | -0.19 |  | Left Off ( Gas drops quick)
LC6B |  | 53.2 | 37.4 | 0.5 | 8.9 | 8 | 4 | 1006 | -28.54 |  | Open Full
PW1 |  | 4.2 | 2.4 | 6.9 | 86.5 | 7 | 8 | 1006 | -0.05 |  | Left Off
PW2 |  | 34 | 20.1 | 2.9 | 43 | 10 | 9 | 1006 | -0.36 |  | Left Off
PW3 |  | 37.2 | 19.9 | 3.5 | 39.4 | 6 | 10 | 1006 | -0.41 |  | Left Off
PW4 |  | 48.5 | 36 | 1.1 | 14.4 | 8 | 3 | 1006 | -4.13 |  | Cracked Open
PW5 |  | 37.2 | 24.1 | 1.6 | 37.1 | 10 | 8 | 1006 | -0.35 |  | Left Off
PW6 |  | 38.4 | 29.9 | 3 | 28.7 | 4 | 7 | 1006 | -0.54 |  | Left Off
Flare | 14:10 | 54.3 | 38.8 | 0.4 | 6.5 | 5 | 10 | 1006 | 170 |  | Engine running 400 KW. Flow 510m3
Please Note: | GV5, GV9.1,GV20,GV21, LC1.1 and RP6.1 decommissioned and capped off.
Chevrons (>>>) Indicate reading is out of range.

## Jan 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-01-04
Weather: | Dry
Wind conditions: | Breezy
Air Temperature: | 4 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:19 | 0 | 1.8 | 20.4 | 77.8 | 0 | 0 | 1002 | 0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:26 | 0.1 | 0.7 | 20.5 | 78.7 | 0 | 0 | 1002 | -0.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:32 | 0 | 2.2 | 20.2 | 77.6 | 0 | 0 | 1002 | 0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:40 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1002 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:50 | 0 | 0.8 | 20.5 | 78.7 | 0 | 0 | 1002 | 0.32 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:42 | 0 | 2 | 20.3 | 77.7 | 0 | 0 | 1002 | 0.36 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:20 | 28.6 | 3.1 | 17.4 | 50.9 | 0 | 0 | 1002 | 0.74 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:26 | 27.9 | 3.2 | 19 | 49.9 | 0 | 0 | 1002 | 0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:35 | 0 | 1.9 | 20.5 | 77.6 | 0 | 0 | 1002 | -0.2 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:50 | 0 | 2.5 | 17.9 | 79.6 | 0 | 0 | 1002 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:56 | 0 | 2.6 | 19.2 | 78.2 | 0 | 0 | 1002 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:02 | 0 | 2.3 | 19 | 78.7 | 0 | 0 | 1002 | -0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:09 | 0 | 1 | 20.2 | 78.8 | 0 | 0 | 1002 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:15 | 0 | 2.3 | 20 | 77.7 | 0 | 0 | 1002 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:20 | 0 | 3.5 | 19.7 | 76.8 | 0 | 0 | 1002 | 0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:30 | 0 | 2.1 | 20 | 77.9 | 0 | 0 | 1002 | 0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:34 | 0 | 2 | 20.2 | 77.8 | 0 | 0 | 1002 | -0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:39 | 0 | 2.4 | 20.1 | 77.5 | 0 | 0 | 1002 | 0.24 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:42 | 0 | 3.9 | 20.4 | 75.7 | 0 | 0 | 1002 | 0.32 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:48 | 0.1 | 2.4 | 20.4 | 77.1 | 0 | 0 | 1002 | 0.1 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:00 | 0 | 2.4 | 19.4 | 78.2 | 0 | 0 | 1002 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:05 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 1002 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:15 | 0 | 3.3 | 20 | 76.7 | 0 | 0 | 1002 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-01-11
Weather: | slight Rain
Wind conditions: | Breezy
Air Temperature: | 2 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:20 | 0 | 1.2 | 21 | 77.8 | 0 | 0 | 1005 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:29 | 0.1 | 0.7 | 21.2 | 78 | 0 | 0 | 1005 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:34 | 0 | 2 | 20.4 | 77.6 | 0 | 0 | 1005 | 0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 10:38 | 0 | 0.6 | 20.8 | 78.6 | 0 | 0 | 1005 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:44 | 0 | 0.7 | 21 | 78.3 | 0 | 0 | 1005 | 0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:28 | 0 | 1.5 | 20.5 | 78 | 0 | 0 | 1005 | 0.17 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:12 | 28 | 3.4 | 13.6 | 55 | 0 | 0 | 1005 | 0.81 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:18 | 24.9 | 6.5 | 17.9 | 50.7 | 0 | 0 | 1005 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:22 | 0 | 1.7 | 21.4 | 76.9 | 0 | 0 | 1005 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:34 | 0 | 2.4 | 14.5 | 83.1 | 0 | 0 | 1005 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:40 | 0 | 2.3 | 18.9 | 78.8 | 0 | 0 | 1005 | -0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:45 | 0 | 1.5 | 18.5 | 80 | 0 | 0 | 1005 | 0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:50 | 0 | 0.8 | 20.9 | 78.3 | 0 | 0 | 1005 | -0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:54 | 0 | 0.9 | 20.7 | 78.4 | 0 | 0 | 1005 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:00 | 0 | 2.3 | 19.9 | 77.8 | 0 | 0 | 1005 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:04 | 0 | 2.4 | 20.4 | 77.2 | 0 | 0 | 1005 | 0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 12:09 | 0.2 | 2 | 21 | 76.8 | 0 | 0 | 1005 | -0.5 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 12:14 | 0 | 0.9 | 20.7 | 78.4 | 0 | 0 | 1005 | -1.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 12:20 | 0 | 4.2 | 21 | 74.8 | 0 | 0 | 1005 | 0.06 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 12:24 | 0.2 | 0.8 | 20.8 | 78.2 | 0 | 0 | 1005 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:00 | 0 | 3 | 19.8 | 77.2 | 0 | 0 | 1005 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:06 | 0 | 1.1 | 20.5 | 78.4 | 0 | 0 | 1005 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:14 | 0 | 1.7 | 20.3 | 78 | 0 | 0 | 1005 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-01-18
Weather: | slight Rain
Wind conditions: | Calm
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:48 | 0 | 1.4 | 21.2 | 77.4 | 0 | 0 | 1000 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:52 | 0.1 | 0.6 | 21 | 78.3 | 0 | 0 | 1000 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 10:59 | 0 | 2.1 | 20.6 | 77.3 | 0 | 0 | 1000 | 0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 11:06 | 0 | 0.7 | 20.5 | 78.8 | 0 | 0 | 1000 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:11 | 0 | 0.6 | 21.3 | 78.1 | 0 | 0 | 1000 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:57 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1000 | 0.21 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:40 | 27.4 | 3 | 14 | 55.6 | 0 | 0 | 1000 | 0.54 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:45 | 22.6 | 7 | 16.9 | 53.5 | 0 | 0 | 1000 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:51 | 0 | 1.6 | 21.3 | 77.1 | 0 | 0 | 1000 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 12:04 | 0 | 2.2 | 15.2 | 82.6 | 0 | 0 | 1000 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 12:11 | 0 | 2.5 | 18.5 | 79 | 0 | 0 | 1000 | -0.12 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 12:17 | 0 | 1.4 | 18.7 | 79.9 | 0 | 0 | 1000 | 0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 12:22 | 0 | 1 | 20.8 | 78.2 | 0 | 0 | 1000 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:28 | 0 | 0.8 | 20.9 | 78.3 | 0 | 0 | 1000 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:36 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1000 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:42 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1000 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 12:48 | 0.1 | 2.1 | 21.4 | 76.4 | 0 | 0 | 1000 | -0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 12:53 | 0 | 0.8 | 20.9 | 78.3 | 0 | 0 | 1000 | -1.12 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 13:00 | 0 | 4.3 | 21.4 | 74.3 | 0 | 0 | 1000 | 0.09 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 13:03 | 0.1 | 0.9 | 20.5 | 78.5 | 0 | 0 | 1000 | -0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:30 | 0 | 3.2 | 20.1 | 76.7 | 0 | 0 | 1000 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:36 | 0 | 1.3 | 20.4 | 78.3 | 0 | 0 | 1000 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 10:42 | 0 | 1.5 | 20.1 | 78.4 | 0 | 0 | 1000 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-01-25
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 3 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:37 | 0 | 1.5 | 21 | 77.5 | 0 | 0 | 1003 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:45 | 0.2 | 0.7 | 21.6 | 77.5 | 0 | 0 | 1003 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:50 | 0 | 2 | 20.4 | 77.6 | 0 | 0 | 1003 | 0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:54 | 0 | 0.8 | 20.9 | 78.3 | 0 | 0 | 1003 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:59 | 0 | 0.7 | 21 | 78.3 | 0 | 0 | 1003 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:50 | 0 | 1.5 | 20.4 | 78.1 | 0 | 0 | 1003 | 0.21 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:30 | 26.9 | 3.2 | 14.5 | 55.4 | 0 | 0 | 1003 | 0.54 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:35 | 20.5 | 6.9 | 16.2 | 56.4 | 0 | 0 | 1003 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:41 | 0 | 1.5 | 21 | 77.5 | 0 | 0 | 1003 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:54 | 0 | 2.5 | 15.4 | 82.1 | 0 | 0 | 1003 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:58 | 0 | 2.1 | 18.3 | 79.6 | 0 | 0 | 1003 | -0.12 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:03 | 0 | 1.6 | 18 | 80.4 | 0 | 0 | 1003 | 0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:07 | 0 | 1.1 | 20.6 | 78.3 | 0 | 0 | 1003 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:12 | 0 | 0.7 | 20.5 | 78.8 | 0 | 0 | 1003 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:18 | 0 | 2 | 20 | 78 | 0 | 0 | 1003 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:24 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1003 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:30 | 0.1 | 2.4 | 21.2 | 76.3 | 0 | 0 | 1003 | -0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:34 | 0 | 0.8 | 20.6 | 78.6 | 0 | 0 | 1003 | -1.12 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:39 | 0 | 4.6 | 21.5 | 73.9 | 0 | 0 | 1003 | 0.09 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:42 | 0.2 | 1 | 20.6 | 78.2 | 0 | 0 | 1003 | -0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:20 | 0 | 3.4 | 20.2 | 76.4 | 0 | 0 | 1003 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:26 | 0 | 1.2 | 20.6 | 78.2 | 0 | 0 | 1003 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:32 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1003 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## Feb 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-02-01
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 8:57 | 0 | 1.5 | 21.1 | 77.4 | 0 | 0 | 1009 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:03 | 0.2 | 0.6 | 21.4 | 77.8 | 0 | 0 | 1009 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:10 | 0 | 2.3 | 20.2 | 77.5 | 0 | 0 | 1009 | 0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:16 | 0 | 0.7 | 20.5 | 78.8 | 0 | 0 | 1009 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:22 | 0 | 0.6 | 21.2 | 78.2 | 0 | 0 | 1009 | 0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:08 | 0 | 1.1 | 20.6 | 78.3 | 0 | 0 | 1009 | 0.17 | 1 | 10 | 0.5 | 5
BK BH 8 | 9:51 | 26.2 | 3.5 | 14.7 | 55.6 | 0 | 0 | 1009 | 0.49 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 9:56 | 18.6 | 7.6 | 16.5 | 57.3 | 0 | 0 | 1009 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:02 | 0 | 1.4 | 20.8 | 77.8 | 0 | 0 | 1009 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:14 | 0 | 2.1 | 15.7 | 82.2 | 0 | 0 | 1009 | 0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:20 | 0 | 2.2 | 18.6 | 79.2 | 0 | 0 | 1009 | -0.1 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:24 | 0 | 1.4 | 18.4 | 80.2 | 0 | 0 | 1009 | 0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:30 | 0 | 1.2 | 20.3 | 78.5 | 0 | 0 | 1009 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:34 | 0 | 0.6 | 20.4 | 79 | 0 | 0 | 1009 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:37 | 0 | 2.1 | 20.1 | 77.8 | 0 | 0 | 1009 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:41 | 0 | 2.5 | 20 | 77.5 | 0 | 0 | 1009 | 0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:48 | 0.2 | 2.5 | 20.8 | 76.5 | 0 | 0 | 1009 | -0.39 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:53 | 0 | 0.7 | 21 | 78.3 | 0 | 0 | 1009 | -1.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:00 | 0 | 4.8 | 21.2 | 74 | 0 | 0 | 1009 | 0.07 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:07 | 0.1 | 1.2 | 20.8 | 77.9 | 0 | 0 | 1009 | -0.05 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 8:40 | 0 | 3.5 | 20.4 | 76.1 | 0 | 0 | 1009 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 8:45 | 0 | 1.3 | 20.8 | 77.9 | 0 | 0 | 1009 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 8:52 | 0 | 1.2 | 20.2 | 78.6 | 0 | 0 | 1009 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-02-08
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 2 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:31 | 0 | 1.7 | 21.2 | 77.1 | 0 | 0 | 1004 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:36 | 0.3 | 0.5 | 20.4 | 78.8 | 0 | 0 | 1004 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | 9:44 | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:49 | 0 | 0.6 | 20.7 | 78.7 | 0 | 0 | 1004 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:55 | 0 | 0.7 | 21 | 78.3 | 0 | 0 | 1004 | 0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:42 | 0 | 1.6 | 20.5 | 77.9 | 0 | 0 | 1004 | 0.12 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:26 | 25.8 | 3.4 | 14.6 | 56.2 | 0 | 0 | 1004 | 0.46 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:31 | 19.9 | 8 | 16.2 | 55.9 | 0 | 0 | 1004 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:36 | 0 | 1.5 | 20.5 | 78 | 0 | 0 | 1004 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:48 | 0 | 2.4 | 15.9 | 81.7 | 0 | 0 | 1004 | 0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:54 | 0 | 2.1 | 18.5 | 79.4 | 0 | 0 | 1004 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:59 | 0 | 1.5 | 18.2 | 80.3 | 0 | 0 | 1004 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:05 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1004 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 11:11 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 1004 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:17 | 0 | 2.2 | 20 | 77.8 | 0 | 0 | 1004 | -0.09 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:22 | 0 | 2.6 | 19.9 | 77.5 | 0 | 0 | 1004 | 0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:25 | 0.1 | 2.2 | 20.5 | 77.2 | 0 | 0 | 1004 | -0.45 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:28 | 0 | 0.8 | 21.4 | 77.8 | 0 | 0 | 1004 | -1.07 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | 11:34 | 0 | 4.5 | 21 | 74.5 | 0 | 0 | 1004 | 0.05 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:40 | 0.1 | 1.6 | 20.5 | 77.8 | 0 | 0 | 1004 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:12 | 0 | 3.1 | 20.1 | 76.8 | 0 | 0 | 1004 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:17 | 0 | 1.2 | 20.9 | 77.9 | 0 | 0 | 1004 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:24 | 0 | 1.1 | 20.5 | 78.4 | 0 | 0 | 1004 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-02-16
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 3 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:17 | 0 | 1.5 | 21.4 | 77.1 | 0 | 0 | 997 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:24 | 0.1 | 0.6 | 20.6 | 78.7 | 0 | 0 | 997 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 9:30 | 0 | 0.5 | 20.9 | 78.6 | 0 | 0 | 997 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:36 | 0 | 0.8 | 21.4 | 77.8 | 0 | 0 | 997 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 10:21 | 0 | 1.7 | 20.6 | 77.7 | 0 | 0 | 997 | 0.16 | 1 | 10 | 0.5 | 5
BK BH 8 | 10:04 | 25.2 | 3.5 | 14.9 | 56.4 | 0 | 0 | 997 | 0.55 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:09 | 19.4 | 9.2 | 16.4 | 55 | 0 | 0 | 997 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:15 | 0 | 1.6 | 20.1 | 78.3 | 0 | 0 | 997 | -0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:27 | 0 | 2.5 | 16.2 | 81.3 | 0 | 0 | 997 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:36 | 0 | 2.4 | 18.9 | 78.7 | 0 | 0 | 997 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:44 | 0 | 1.7 | 18.7 | 79.6 | 0 | 0 | 997 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:48 | 0 | 1.2 | 20.2 | 78.6 | 0 | 0 | 997 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:53 | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 997 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:00 | 0 | 2.3 | 20.3 | 77.4 | 0 | 0 | 997 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:06 | 0 | 2.4 | 19.8 | 77.8 | 0 | 0 | 997 | 0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 11:12 | 0 | 1.2 | 20.1 | 78.7 | 0 | 0 | 997 | -0.41 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 11:19 | 0 | 0.9 | 21.1 | 78 | 0 | 0 | 997 | -1.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried Investigating | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 11:31 | 0.1 | 1.9 | 20.4 | 77.6 | 0 | 0 | 997 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:00 | 0 | 3.4 | 20.3 | 76.3 | 0 | 0 | 997 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:06 | 0 | 1.4 | 20.7 | 77.9 | 0 | 0 | 997 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:12 | 0 | 1.3 | 20 | 78.7 | 0 | 0 | 997 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-02-22
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 3 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS/MJ
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 8:23 | 0 | 0.9 | 21.1 | 78 | 0 | 0 | 1007 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 8:28 | 0 | 0.6 | 21.3 | 78.1 | 0 | 0 | 1007 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 8:36 | 0 | 0.7 | 21.2 | 78.1 | 0 | 0 | 1007 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 8:41 | 0 | 0.6 | 21.4 | 78 | 0 | 0 | 1007 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 9:07 | 0 | 1.1 | 21.1 | 77.8 | 0 | 0 | 1007 | 0.2 | 1 | 10 | 0.5 | 5
BK BH 8 | 8:49 | 25 | 3.4 | 11.8 | 59.8 | 0 | 0 | 1007 | 0.9 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 8:55 | 10.8 | 8.5 | 17.4 | 63.3 | 0 | 0 | 1007 | -0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 9:01 | 0 | 1.8 | 21.1 | 77.1 | 0 | 0 | 1007 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 9:14 | 0 | 2.3 | 13.2 | 84.5 | 0 | 0 | 1007 | 0.1 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 9:20 | 0 | 2.2 | 18.6 | 79.2 | 0 | 0 | 1007 | -0.28 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 9:26 | 0 | 1.2 | 18.9 | 79.9 | 0 | 0 | 1007 | 0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 9:32 | 0 | 0.6 | 21.1 | 78.3 | 0 | 0 | 1007 | -0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 9:35 | 0 | 0.5 | 21.2 | 78.3 | 0 | 0 | 1007 | -0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 9:41 | 0 | 2.1 | 19.8 | 78.1 | 0 | 0 | 1007 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | Flooded | [8 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:50 | 0 | 0.5 | 21.2 | 78.3 | 0 | 0 | 1007 | -0.79 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:00 | 0 | 0.6 | 20.8 | 78.6 | 0 | 0 | 1007 | -2 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried investigating | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:15 | 0 | 0.5 | 21.1 | 78.4 | 0 | 0 | 1007 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 8:10 | 0 | 3.5 | 19 | 77.5 | 0 | 0 | 1007 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 8:14 | 0 | 1.2 | 20.9 | 77.9 | 0 | 0 | 1007 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 8:19 | 0 | 1.4 | 20 | 78.6 | 0 | 0 | 1007 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## March 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-03-01
Weather: | Dry
Wind conditions: | Calm
Air Temperature: | 3 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS/MJ
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 11:05 | 0 | 0.5 | 20.5 | 79 | 0 | 0 | 1002 | -0.5 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 11:10 | 0 | 0.3 | 19.9 | 79.8 | 0 | 0 | 1002 | 0.71 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 11:17 | 0 | 0.5 | 20.4 | 79.1 | 0 | 0 | 1002 | 0.63 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 11:21 | 0 | 1.1 | 20 | 78.9 | 0 | 0 | 1002 | -0.15 | 1 | 10 | 0.5 | 5
BK BH 8 | 11:24 | 20.3 | 3.4 | 11.8 | 64.5 | 0 | 0 | 1002 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 11:30 | 19.2 | 8.5 | 16.2 | 56.1 | 0 | 0 | 1002 | -0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 11:35 | 0 | 1.6 | 21.1 | 77.3 | 0 | 0 | 1002 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 11:47 | 0 | 2 | 13.2 | 84.8 | 0 | 0 | 1002 | 0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 11:51 | 0 | 2.1 | 18.6 | 79.3 | 0 | 0 | 1002 | -0.87 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 11:55 | 0 | 1.4 | 18.9 | 79.7 | 0 | 0 | 1002 | 0.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 11:58 | 0 | 0.4 | 21.1 | 78.5 | 0 | 0 | 1002 | -0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 12:01 | 0 | 0.6 | 20.3 | 79.1 | 0 | 0 | 1002 | -0.14 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 12:04 | 0.1 | 2 | 20.6 | 77.3 | 0 | 0 | 1002 | 0.69 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 12:11 | 0.2 | 3 | 19.2 | 77.6 | 0 | 0 | 1002 | 0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 10:37 | 0 | 0.6 | 21.2 | 78.2 | 0 | 0 | 1002 | -0.47 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 10:41 | 0 | 0.7 | 20.8 | 78.5 | 0 | 0 | 1002 | -0.15 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:49 | 0 | 0.4 | 21.1 | 78.5 | 0 | 0 | 1002 | -0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 10:54 | 0 | 4.6 | 16.2 | 79.2 | 0 | 0 | 1002 | 0.71 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 10:57 | 0 | 0.6 | 18.9 | 80.5 | 0 | 0 | 1002 | 0.36 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 11:01 | 0 | 0.6 | 18.9 | 80.5 | 0 | 0 | 1002 | -0.17 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-03-08
Weather: | Dry
Wind conditions: | Slight breeze
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS/MJ
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 10:03 | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 997 | -0.5 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 10:08 | 0 | 0.2 | 19.9 | 79.9 | 0 | 0 | 997 | 0.71 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 10:15 | 0 | 0.6 | 20.6 | 78.8 | 0 | 0 | 997 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | Flooded | [8 empty] | 1 | 10 | 0.5 | 5
BK BH 8 | 10:22 | 19.9 | 3 | 11.9 | 65.2 | 0 | 0 | 997 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:28 | 20.2 | 8.4 | 17 | 54.4 | 0 | 0 | 997 | 0.94 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:33 | 0 | 1.4 | 19.9 | 78.7 | 0 | 0 | 997 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:45 | 0 | 2.1 | 14.2 | 83.7 | 0 | 0 | 997 | -0.65 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:49 | 0 | 2.6 | 18.9 | 78.5 | 0 | 0 | 997 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:53 | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 997 | -0.1 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:56 | 0 | 0.5 | 20.9 | 78.6 | 0 | 0 | 997 | 0.45 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:59 | 0 | 0.7 | 20.4 | 78.9 | 0 | 0 | 997 | -0.18 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 11:02 | 0.2 | 2.1 | 20.3 | 77.4 | 0 | 0 | 997 | 0.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 11:09 | 0.1 | 2.6 | 19.5 | 77.8 | 0 | 0 | 997 | -0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:35 | 0 | 0.9 | 20.1 | 79 | 0 | 0 | 997 | -0.47 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:39 | 0 | 0.8 | 20.3 | 78.9 | 0 | 0 | 997 | -0.15 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  | 100 |  |  |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:47 | 0 | 0.6 | 20.4 | 79 | 0 | 0 | 997 | -0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:52 | 0 | 4.5 | 16.8 | 78.7 | 0 | 0 | 997 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:55 | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 997 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:59 | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 997 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-03-15
Weather: | Dry
Wind conditions: | Slight breeze
Air Temperature: | 4 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS/MJ
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:24 | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 995 | -0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:29 | 0 | 0.3 | 19.6 | 80.1 | 0 | 0 | 995 | -0.23 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:36 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 995 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | Flooded | [8 empty] | 1 | 10 | 0.5 | 5
BK BH 8 | 9:43 | 18.6 | 3 | 12.8 | 65.6 | 0 | 0 | 995 | -0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 9:49 | 19.5 | 8.1 | 18.6 | 53.8 | 0 | 0 | 995 | -0.23 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 9:54 | 0 | 1.5 | 19.3 | 79.2 | 0 | 0 | 995 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:06 | 0 | 2.2 | 14.1 | 83.7 | 0 | 0 | 995 | -0.41 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:10 | 0 | 2.4 | 18.6 | 79 | 0 | 0 | 995 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:14 | 0 | 1.2 | 19.1 | 79.7 | 0 | 0 | 995 | -0.1 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:17 | 0 | 0.4 | 20.5 | 79.1 | 0 | 0 | 995 | 0.14 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:20 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 995 | -0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:23 | 0.3 | 2.2 | 19.8 | 77.7 | 0 | 0 | 995 | 0.09 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:30 | 0.1 | 2.4 | 19.6 | 77.9 | 0 | 0 | 995 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 8:56 | 0 | 0.8 | 19.7 | 79.5 | 0 | 0 | 995 | -0.49 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:00 | 0 | 0.7 | 20.1 | 79.2 | 0 | 0 | 995 | -0.1 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:08 | 0 | 0.4 | 20 | 79.6 | 0 | 0 | 995 | -0.26 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:13 | 0 | 4.2 | 17.2 | 78.6 | 0 | 0 | 995 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:16 | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 995 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:20 | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 995 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-03-22
Weather: | Dry
Wind conditions: | Slight breeze
Air Temperature: | 5 | OC
Instrument: | GA 2000
Serial No: | GA10692/08
Calibrated To: | 2018-06-13
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 9:41 | 0 | 0.6 | 19.8 | 79.6 | 0 | 0 | 1003 | -0.16 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 9:46 | 0 | 0.4 | 19.7 | 79.9 | 0 | 0 | 1003 | -0.21 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 9:53 | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1003 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | Flooded | [8 empty] | 1 | 10 | 0.5 | 5
BK BH 8 | 10:00 | 17.9 | 2.8 | 13.2 | 66.1 | 0 | 0 | 1003 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 10:06 | 18.6 | 8 | 18.9 | 54.5 | 0 | 0 | 1003 | -0.23 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 10:11 | 0 | 1.4 | 19.5 | 79.1 | 0 | 0 | 1003 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 10:23 | 0 | 2.4 | 14.5 | 83.1 | 0 | 0 | 1003 | -0.36 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 10:27 | 0 | 2.1 | 18.7 | 79.2 | 0 | 0 | 1003 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 10:31 | 0 | 1.1 | 19.5 | 79.4 | 0 | 0 | 1003 | -0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 10:34 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 1003 | 0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 10:37 | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1003 | -0.12 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 10:40 | 0.2 | 2.5 | 19.6 | 77.7 | 0 | 0 | 1003 | 0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | 10:47 | 0.3 | 2.1 | 19.7 | 77.9 | 0 | 0 | 1003 | -0.2 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:13 | 0 | 0.5 | 19.3 | 80.2 | 0 | 0 | 1003 | -0.34 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:17 | 0 | 0.6 | 20 | 79.4 | 0 | 0 | 1003 | -0.14 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 9:25 | 0 | 0.4 | 19.8 | 79.8 | 0 | 0 | 1003 | -0.23 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 9:30 | 0 | 4.3 | 17.5 | 78.2 | 0 | 0 | 1003 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 9:33 | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 1003 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 9:37 | 0 | 0.7 | 19.1 | 80.2 | 0 | 0 | 1003 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-03-26
Weather: | Partly Cloudy
Wind conditions: | Light Breeze
Air Temperature: | 3 | OC
Instrument: | Gem 2000 Plus
Serial No: | GM12289
Calibrated To: | 2018-09-14
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 | 8:27 | 0 | 0.8 | 21 | 78.2 | 0 | 0 | 1018 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | 8:32 | 0 | 0.7 | 20.4 | 78.9 | 0 | 0 | 1018 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | 8:37 | 0 | 0.9 | 20.5 | 78.6 | 0 | 0 | 1018 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | 8:42 | 0 | 0.9 | 21.1 | 78 | 0 | 0 | 1018 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | 9:02 | 0 | 1.3 | 20.8 | 77.9 | 0 | 0 | 1018 | 0.16 | 1 | 10 | 0.5 | 5
BK BH 8 | 8:46 | 25.8 | 3.2 | 11.4 | 59.6 | 0 | 0 | 1018 | 0.8 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 | 8:51 | 19.9 | 8.2 | 17.9 | 54 | 0 | 0 | 1018 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 | 8:56 | 0 | 1.5 | 20.9 | 77.6 | 0 | 0 | 1018 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 | 9:06 | 0 | 2.5 | 13.9 | 83.6 | 0 | 0 | 1018 | 0.1 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 | 9:10 | 0 | 2.3 | 18.7 | 79 | 0 | 0 | 1018 | -0.18 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 | 9:18 | 0 | 1.4 | 19.3 | 79.3 | 0 | 0 | 1018 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 | 9:25 | 0 | 0.5 | 20.8 | 78.7 | 0 | 0 | 1018 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 | 9:32 | 0 | 0.8 | 21 | 78.2 | 0 | 0 | 1018 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | 9:38 | 0 | 2.3 | 19.6 | 78.1 | 0 | 0 | 1018 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | Flooded | [8 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 | 9:43 | 0 | 0.6 | 21 | 78.4 | 0 | 0 | 1018 | -0.54 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 | 9:52 | 0 | 0.4 | 20.5 | 79.1 | 0 | 0 | 1018 | -1.58 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 | 10:08 | 0 | 0.7 | 20.8 | 78.5 | 0 | 0 | 1018 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 | 8:15 | 0 | 3.2 | 19.3 | 77.5 | 0 | 0 | 1018 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 | 8:19 | 0 | 1.4 | 20.5 | 78.1 | 0 | 0 | 1018 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 | 8:24 | 0 | 1.5 | 19.9 | 78.6 | 0 | 0 | 1018 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## April 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-04-05
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA13543
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 996 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 | Flooded | [8 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.3 | 20.7 | 78 | 0 | 0 | 996 | -0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 21 | 78.8 | 0 | 0 | 996 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 20.2 | 79.5 | 0 | 0 | 996 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.1 | 3 | 15.1 | 68.8 | 0 | 0 | 996 | -0.65 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.2 | 9.1 | 15.9 | 59.8 | 0 | 0 | 996 | -0.94 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 20.8 | 79.1 | 0 | 0 | 996 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.4 | 6.7 | 90.9 | 0 | 0 | 996 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.3 | 19.8 | 79.9 | 0 | 0 | 996 | -0.1 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.7 | 12.5 | 85.8 | 0 | 0 | 996 | 0.45 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 20.9 | 79.1 | 0 | 0 | 996 | -0.18 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0 | 20.9 | 79.1 | 0 | 0 | 996 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.3 | 0.1 | 21 | 78.6 | 0 | 0 | 996 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.8 | 20.2 | 78.9 | 0 | 0 | 996 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 21.2 | 78.8 | 0 | 0 | 996 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.4 | 2.8 | 21 | 75.8 | 0 | 0 | 996 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 996 | -0.89 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4.4 | 14.3 | 81.2 | 0 | 0 | 996 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 18.5 | 81.4 | 0 | 0 | 996 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.1 | 18.5 | 81.4 | 0 | 0 | 996 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-04-10
Weather: | Drizzle
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA13543
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0 | 19.7 | 80.3 | 0 | 0 | 988 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 19.8 | 80.2 | 0 | 0 | 988 | -0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 19.7 | 80 | 0 | 0 | 988 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 20.2 | 79.5 | 0 | 0 | 988 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.3 | 3 | 15.2 | 68.5 | 0 | 0 | 988 | 0 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.3 | 9.2 | 15.2 | 60.3 | 0 | 0 | 988 | -0.13 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 19.9 | 80 | 0 | 0 | 988 | -0.12 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.7 | 11.6 | 86.7 | 0 | 0 | 988 | 1.1 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.9 | 15.9 | 83.2 | 0 | 0 | 988 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.7 | 12.5 | 85.8 | 0 | 0 | 988 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 19.9 | 80.1 | 0 | 0 | 988 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 19.7 | 80.2 | 0 | 0 | 988 | -0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.7 | 0.9 | 18.1 | 80.3 | 0 | 0 | 988 | 0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.8 | 20.2 | 78.9 | 0 | 0 | 988 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 988 | 1.66 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.4 | 2.8 | 21 | 75.8 | 0 | 0 | 988 | -0.08 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.8 | 18.3 | 80.9 | 0 | 0 | 988 | 2.95 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.1 | 14.2 | 80.7 | 0 | 0 | 988 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.9 | 18.6 | 80.5 | 0 | 0 | 988 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0 | 19.8 | 80.2 | 0 | 0 | 988 | -0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-04-19
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA13543
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 1006 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 19.5 | 80.5 | 0 | 0 | 1006 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 19.3 | 80.5 | 0 | 0 | 1006 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.2 | 2.2 | 20.1 | 77.5 | 0 | 0 | 1006 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.1 | 2.9 | 15.7 | 68.3 | 0 | 0 | 1006 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 13.7 | 7.7 | 15.2 | 63.4 | 0 | 0 | 1006 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 1006 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 13.8 | 84.7 | 0 | 0 | 1006 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 16.7 | 82.5 | 0 | 0 | 1006 | -0.37 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1006 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 19.2 | 80.8 | 0 | 0 | 1006 | -0.32 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 1006 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 0.8 | 16.6 | 82 | 0 | 0 | 1006 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 1 | 16.8 | 82 | 0 | 0 | 1006 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 19 | 81 | 0 | 0 | 1006 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 3.2 | 20.1 | 76.4 | 0 | 0 | 1006 | -0.05 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.8 | 17.5 | 81.7 | 0 | 0 | 1006 | -1 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.1 | 13.2 | 81.7 | 0 | 0 | 1006 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 19.4 | 80.6 | 0 | 0 | 1006 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.7 | 17.8 | 81.5 | 0 | 0 | 1006 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-04-25
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA13543
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.8 | 19.5 | 78.4 | 0 | 0 | 992 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.8 | 21 | 78.2 | 0 | 0 | 993 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 22.1 | 77.8 | 0 | 0 | 992 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 22 | 78 | 0 | 0 | 993 | 0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.8 | 3.5 | 19.1 | 71.6 | 0 | 0 | 993 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.6 | 9.7 | 16.5 | 58.2 | 0 | 0 | 994 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 22.1 | 77.8 | 0 | 0 | 992 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 5.1 | 3.3 | 91.6 | 0 | 0 | 993 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.2 | 19.9 | 78.9 | 0 | 0 | 993 | -0.01 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.9 | 20 | 79.1 | 0 | 0 | 992 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 21.9 | 78 | 0 | 0 | 992 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 21.6 | 78 | 0 | 0 | 992 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.8 | 0.5 | 20.2 | 78.5 | 0 | 0 | 992 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 2 | 20 | 77.9 | 0 | 0 | 992 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.8 | 20.1 | 79.1 | 0 | 0 | 992 | 0.48 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 0.5 | 19.9 | 79.3 | 0 | 0 | 992 |  | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.1 | 20.9 | 78 | 0 | 0 | 992 | -0.39 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.3 | 16.2 | 78.5 | 0 | 0 | 992 | -0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 21.8 | 78.1 | 0 | 0 | 992 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.2 | 19.7 | 78.1 | 0 | 0 | 992 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA13543 | MCERTS certified instrument
Date downloaded | 2018-04-19 21:24 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-04-19
Date of last factory calibration | 2018-03-06
Next service due | 2018-09-06
Date of last Gas Check | 2018-03-06
Security code | [58638ACF]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | SITECHOSEN 1 | SITECHOSEN 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-04-19 11:26 | 57.9 | 38.4 | 0.2 | 3.5 | 1005 | 182.74 | 1 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0035 | 2018-04-19 11:34 | 56.1 | 38.5 | 1.3 | 4.1 | 1005 | 1.09 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0036 | 2018-04-19 11:38 | 43.1 | 25.9 | 3.4 | 27.6 | 1005 | 0.01 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0037 | 2018-04-19 11:42 | 53.1 | 31 | 2 | 13.9 | 1005 | -0.1 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHM010MB | 2018-04-19 11:45 | 60.1 | 41.6 | 0.9 | 0 | 1005 | -18.77 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0018 | 2018-04-19 12:24 | 60 | 42.3 | 1 | 0 | 1004 | -20.82 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHR0004B | 2018-04-19 12:30 | 43.5 | 30.5 | 6 | 20 | 1005 | 3.64 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0015 | 2018-04-19 12:31 | 59 | 42.5 | 1.2 | 0 | 1005 | -18.66 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0014 | 2018-04-19 12:33 | 60.1 | 40.2 | 0.9 | 0 | 1005 | -19.48 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0013 | 2018-04-19 12:34 | 2.4 | 5 | 17.6 | 75 | 1005 | 0.09 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0016 | 2018-04-19 12:38 | 43.4 | 34.6 | 5.3 | 16.7 | 1005 | -0.17 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHL000C4 | 2018-04-19 12:40 | 37.8 | 24.5 | 4.8 | 32.9 | 1005 | 0 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0017 | 2018-04-19 12:46 | 61.3 | 41.2 | 0.9 | 0 | 1004 | 7.58 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHM010MA | 2018-04-19 12:48 | 59.1 | 41.6 | 0.9 | 0 | 1005 | -19.18 | 0 | 1 | LOW | fully open |  | Sunny | light wind
BHGV0038 | 2018-04-19 12:52 | 63.3 | 33.9 | 1.7 | 1.1 | 1005 | -0.1 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHGV0038 | 2018-04-19 12:53 | 63.2 | 34.1 | 1.6 | 1.1 | 1005 | -1.38 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0039 | 2018-04-19 12:57 | 65.8 | 35.4 | 1.1 | 0 | 1005 | -1.16 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHGV0039 | 2018-04-19 12:58 | 65.8 | 35.5 | 1.1 | 0 | 1005 | -3.63 | 0 | 1 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0011 | 2018-04-19 13:01 | 28.7 | 27.3 | 2.3 | 41.7 | 1005 | -1.6 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0010 | 2018-04-19 13:03 | 52.5 | 32.2 | 2 | 13.3 | 1005 | -8.66 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0040 | 2018-04-19 13:06 | 54.3 | 33.9 | 1.4 | 10.4 | 1005 | -9.78 | 0 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0040 | 2018-04-19 13:06 | 54.1 | 33.9 | 1.4 | 10.6 | 1005 | -11.95 | 0 | 1 | LOW | partially open | no vacuum change | Sunny | light wind
BHLC001B | 2018-04-19 13:08 | 0 | 2.7 | 19.9 | 77.4 | 1005 | -1.32 | 1 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0009 | 2018-04-19 13:11 | 63.5 | 37.5 | 0.8 | 0 | 1005 | -1.13 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHGV0009 | 2018-04-19 13:12 | 63.2 | 37.5 | 1 | 0 | 1005 | -10.56 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHLC0003 | 2018-04-19 13:17 | 13.6 | 9.9 | 14.1 | 62.4 | 1005 | -0.96 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0301 | 2018-04-19 13:20 | 64.9 | 39.1 | 0.9 | 0 | 1004 | -15.99 | 1 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0301 | 2018-04-19 13:21 | 63.7 | 38.9 | 1 | 0 | 1005 | -16.12 | 0 | 1 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0012 | 2018-04-19 13:25 | 59.5 | 39.7 | 1 | 0 | 1004 | -15.25 | 0 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0012 | 2018-04-19 13:25 | 58.9 | 39.9 | 1.1 | 0.1 | 1004 | -15.58 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHR00003 | 2018-04-19 13:33 | 0 | 3 | 19.6 | 77.4 | 1004 | -0.62 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0046 | 2018-04-19 13:36 | 50.7 | 35.3 | 0.9 | 13.1 | 1004 | -9.51 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0042 | 2018-04-19 13:40 | 66.7 | 31 | 1.4 | 0.9 | 1005 | -2.84 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHGV0042 | 2018-04-19 13:41 | 66.6 | 31.1 | 1.5 | 0.8 | 1005 | -3.43 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0043 | 2018-04-19 13:44 | 26.7 | 18.4 | 9.8 | 45.1 | 1005 | -15.05 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0007 | 2018-04-19 13:49 | 63 | 29.1 | 0.9 | 7 | 1005 | -2.08 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHGV0007 | 2018-04-19 13:51 | 62 | 29 | 1.1 | 7.9 | 1005 | -5.13 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0008 | 2018-04-19 13:53 | 19.9 | 13.2 | 12.3 | 54.6 | 1005 | -9.86 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHLC002R | 2018-04-19 13:55 | 59.1 | 33.5 | 0.6 | 6.8 | 1005 | -16.43 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHLC002R | 2018-04-19 13:55 | 58.7 | 33.8 | 0.6 | 6.9 | 1005 | -16.53 | 1 | 1 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0044 | 2018-04-19 13:57 | 36.1 | 23.8 | 4.9 | 35.2 | 1005 | -5.74 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHR00001 | 2018-04-19 14:04 | 54.9 | 33.4 | 2.8 | 8.9 | 1004 | -16.21 | 1 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0001 | 2018-04-19 14:07 | 47.7 | 28.1 | 5.2 | 19 | 1004 | -15.63 | 1 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0045 | 2018-04-19 14:14 | 25.2 | 18.1 | 11.1 | 45.6 | 1004 | -2.35 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0021 | 2018-04-19 14:23 | 46.6 | 23.5 | 5.9 | 24 | 1006 | -4.65 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0006 | 2018-04-19 14:26 | 47.3 | 36.4 | 3.7 | 12.6 | 1006 | -0.39 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0003 | 2018-04-19 14:27 | 68 | 36.3 | 0.3 | 0 | 1006 | -16.21 | 0 | 0 | LOW | fully open |  | Sunny | light wind
BHR0001B | 2018-04-19 14:28 | 67.8 | 35.8 | 0.7 | 0 | 1006 | 0.05 | 0 | 0 | LOW | closed |  | Sunny | light wind
BHGV0004 | 2018-04-19 14:35 | 69.4 | 28.4 | 2 | 0.2 | 1006 | -30.31 | 1 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHLC002B | 2018-04-19 14:39 | 69 | 28.5 | 2.5 | 0 | 1005 | -0.15 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0047 | 2018-04-19 14:41 | 0 | 2.3 | 19.1 | 78.6 | 1005 | -3.14 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHM050MB | 2018-04-19 14:44 | 58.3 | 36.7 | 0.8 | 4.2 | 1005 | -16.59 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0025 | 2018-04-19 14:48 | 59.5 | 33.6 | 0.3 | 6.6 | 1005 | -8.3 | 0 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0025 | 2018-04-19 14:48 | 56.6 | 33.5 | 0.3 | 9.6 | 1005 | -18.88 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV000A | 2018-04-19 14:50 | 35.8 | 21.9 | 4.9 | 37.4 | 1005 | -5.42 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0024 | 2018-04-19 14:52 | 63.2 | 38.6 | 0.2 | 0 | 1005 | -15.18 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0023 | 2018-04-19 14:53 | 0.3 | 11.4 | 12.8 | 75.5 | 1005 | 0.02 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0048 | 2018-04-19 14:54 | 63.9 | 38 | 0.3 | 0 | 1005 | -14.4 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0022 | 2018-04-19 14:56 | 0 | 6.8 | 16.9 | 76.3 | 1005 | 0 | 0 | 0 | LOW | closed |  | Sunny | light wind
BHM050MA | 2018-04-19 14:59 | 57.6 | 36.6 | 0.8 | 5 | 1005 | -15.06 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHLC0006 | 2018-04-19 15:04 | 60.1 | 42.2 | 0.3 | 0 | 1004 | 0.61 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHLC006B | 2018-04-19 15:06 | 59.1 | 43.2 | 0.2 | 0 | 1003 | -0.53 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHLC006B | 2018-04-19 15:07 | 59.2 | 43.6 | 0.2 | 0 | 1003 | -1.71 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHLC0005 | 2018-04-19 15:11 | 43.4 | 40.4 | 3.2 | 13 | 1003 | 0.21 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0029 | 2018-04-19 15:13 | 61 | 42.3 | 0.1 | 0 | 1003 | -14.38 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0028 | 2018-04-19 15:18 | 56.7 | 42.2 | 0.5 | 0.6 | 1003 | -6.3 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0028 | 2018-04-19 15:19 | 56.7 | 42.3 | 0.6 | 0.4 | 1003 | -8.55 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0027 | 2018-04-19 15:22 | 58.8 | 41.6 | 0.1 | 0 | 1004 | -13.37 | 0 | 1 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV0026 | 2018-04-19 15:28 | 59.2 | 38.6 | 0 | 2.2 | 1004 | -13.35 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHR0002B | 2018-04-19 15:30 | 59.2 | 38.4 | 0.2 | 2.2 | 1004 | -16.74 | 0 | 0 | LOW | fully open | no vacuum change | Sunny | light wind
BHGV000B | 2018-04-19 15:37 | 58.7 | 37.6 | 0 | 3.7 | 1003 | -12.33 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0030 | 2018-04-19 15:40 | 57.8 | 38.2 | 0 | 4 | 1003 | -8.1 | 0 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0030 | 2018-04-19 15:40 | 57.6 | 38.9 | 0 | 3.5 | 1003 | -9.14 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV000C | 2018-04-19 15:41 | 58.4 | 40.9 | 0 | 0.7 | 1003 | -7.98 | 0 | 1 | LOW | partially open | no vacuum change | Sunny | light wind
BHR00005 | 2018-04-19 15:44 | 1 | 6.5 | 4.8 | 87.7 | 1003 | -0.57 | 1 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGV0031 | 2018-04-19 15:46 | 60.9 | 39.2 | 0.1 | 0 | 1004 | -11.83 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0032 | 2018-04-19 15:49 | 48.3 | 37.2 | 3.1 | 11.4 | 1004 | -1.18 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0033 | 2018-04-19 15:52 | 60.5 | 42.2 | 0 | 0 | 1004 | -2.19 | 0 | 0 | LOW | partially open | vacuum increased | Sunny | light wind
BHGV0033 | 2018-04-19 15:52 | 60.5 | 40 | 0.1 | 0 | 1004 | -6.13 | 1 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHR0006B | 2018-04-19 15:54 | 59.1 | 40.8 | 0.1 | 0 | 1004 | -1.71 | 0 | 0 | LOW | partially open | no vacuum change | Sunny | light wind
BHGV0049 | 2018-04-19 15:56 | 53.1 | 38.1 | 2.4 | 6.4 | 1004 | 0.02 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHPW0006 | 2018-04-19 16:00 | 7.9 | 22.1 | 12.6 | 57.4 | 1005 | 2.25 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHPW0005 | 2018-04-19 16:03 | 63.3 | 38 | 0.3 | 0 | 1005 | -12.29 | 0 | 0 | LOW | closed | vacuum increased | Sunny | light wind
BHPW0004 | 2018-04-19 16:05 | 33.5 | 26.2 | 4.5 | 35.8 | 1005 | -8.05 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHPW0003 | 2018-04-19 16:07 | 42.2 | 19.6 | 6.5 | 31.7 | 1005 | -12.48 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHPW0002 | 2018-04-19 16:08 | 36.3 | 20.6 | 6.5 | 36.6 | 1005 | 2.88 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHPW0001 | 2018-04-19 16:10 | 6.1 | 8.7 | 16.5 | 68.7 | 1005 | -12.68 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHGW0034 | 2018-04-19 16:11 | 23.6 | 15.9 | 3.4 | 57.1 | 1005 | 0.07 | 0 | 0 | LOW | closed | no vacuum change | Sunny | light wind
BHG01MDA | 2018-04-19 16:14 | 58.1 | 37.4 | 0.3 | 4.2 | 1005 | 190.96 | 1 | 0 | LOW | fully open | no vacuum change | Sunny | light wind

## May 2018
Date | 2018-05-03
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA13543
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1001 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 18 | 81.4 | 0 | 0 | 1001 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 18.6 | 81.3 | 0 | 0 | 1003 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0 | 18.6 | 81.3 | 0 | 0 | 1002 | 0 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.5 | 0.4 | 18.2 | 80.9 | 0 | 0 | 1001 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.1 | 5 | 17.2 | 67.7 | 0 | 0 | 1001 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.1 | 18.6 | 81.2 | 0 | 0 | 1002 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 4.5 | 5.1 | 90.4 | 0 | 0 | 1002 | 0.93 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.5 | 6.2 | 90.3 | 0 | 0 | 1002 | -0.2 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 1002 | 0.94 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18.7 | 81.2 | 0 | 0 | 1001 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 18.6 | 81.2 | 0 | 0 | 1001 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.1 | 18.7 | 81.1 | 0 | 0 | 1001 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 18.8 | 81.2 | 0 | 0 | 1001 | 0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.1 | 14.8 | 83.1 | 0 | 0 | 1001 | -0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 0.6 | 19.8 | 79.4 | 0 | 0 | 1001 | 0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.4 | 1.4 | 17.2 | 81 | 0 | 0 | 1001 | 0 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.1 | 16 | 79.9 | 0 | 0 | 1001 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 18.4 | 81.6 | 0 | 0 | 1001 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.5 | 15.9 | 81.6 | 0 | 0 | 1001 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-05-10
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA12599
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.3 | 18.7 | 80.9 | 0 | 0 | 998 | 0.26 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.6 | 17.3 | 81 | 0 | 0 | 998 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.2 | 18.8 | 80.9 | 0 | 0 | 1000 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0 | 19 | 80.9 | 0 | 0 | 1000 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.5 | 3.5 | 15.2 | 73.8 | 0 | 0 | 1000 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.1 | 5.1 | 16.3 | 69.5 | 0 | 0 | 1000 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0 | 19 | 80.9 | 0 | 0 | 999 | 0.82 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 5.3 | 4.5 | 90 | 0 | 0 | 999 | -1.82 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 3.8 | 6.1 | 90 | 0 | 0 | 1000 | -11.18 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 1.2 | 18.1 | 80.5 | 0 | 0 | 999 | 2.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0 | 18.9 | 80.9 | 0 | 0 | 999 | 0 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.3 | 18.7 | 80.9 | 0 | 0 | 999 | 0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.4 | 0.5 | 17.1 | 82 | 0 | 0 | 999 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 0 | 18.9 | 80.9 | 0 | 0 | 999 | 0.32 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 0.3 | 18.1 | 81.4 | 0 | 0 | 998 | -1.6 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 0 | 15.3 | 84.6 | 0 | 0 | 998 | -0.05 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.8 | 16 | 81.1 | 0 | 0 | 998 | -9.84 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4.7 | 15 | 80.2 | 0 | 0 | 998 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 18.9 | 81 | 0 | 0 | 998 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 3 | 16.4 | 80.5 | 0 | 0 | 998 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-05-17
Weather: | drizzle
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1012 | 0.11 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 15.5 | 83.6 | 0 | 0 | 1013 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1014 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 1015 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5 | 1.2 | 12.3 | 81.5 | 0 | 0 | 1014 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.3 | 4.9 | 14.9 | 71.9 | 0 | 0 | 1014 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 16.3 | 83.6 | 0 | 0 | 1014 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 3.4 | 94.3 | 0 | 0 | 1013 | -0.43 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.4 | 5.9 | 91.7 | 0 | 0 | 1014 | 0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 1.3 | 18.3 | 80.3 | 0 | 0 | 1012 | 2.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 16.9 | 83 | 0 | 0 | 1013 | -0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 17 | 82.6 | 0 | 0 | 1013 | -0.12 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.2 | 17 | 82.8 | 0 | 0 | 1014 | 0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.2 | 82.7 | 0 | 0 | 1013 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.8 | 8 | 4 | 87.2 | 0 | 0 | 1011 | -5.17 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 13.2 | 86.6 | 0 | 0 | 1011 | 0.18 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.6 | 16.2 | 81.1 | 0 | 0 | 1011 | -2.32 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.3 | 13.8 | 83.9 | 0 | 0 | 1011 | 0.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 1011 | 0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.5 | 15.3 | 82.2 | 0 | 0 | 1011 | 0.18 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-05-23
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 16.3 | 83.5 | 0 | 0 | 1009 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.4 | 15.2 | 83.4 | 0 | 0 | 1010 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 16.4 | 83.4 | 0 | 0 | 1011 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 16.4 | 83.5 | 0 | 0 | 1011 | 0 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.3 | 3.3 | 12.3 | 76.1 | 0 | 0 | 1010 | -0.38 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.4 | 6.5 | 13.6 | 68.5 | 0 | 0 | 1010 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 16.5 | 83.4 | 0 | 0 | 1010 | -0.08 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 4.5 | 6.9 | 88.6 | 0 | 0 | 1009 | 0.18 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.2 | 5.5 | 90.3 | 0 | 0 | 1009 | 0.07 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 16 | 83.7 | 0 | 0 | 1009 | 0.28 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.3 | 0 | 16.2 | 83.5 | 0 | 0 | 1009 | -0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16 | 83.8 | 0 | 0 | 1008 | -0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 0.9 | 14.2 | 84.3 | 0 | 0 | 1008 | -0.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 16.1 | 83.9 | 0 | 0 | 1008 | -0.12 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.3 | 9.8 | 1.5 | 88.4 | 0 | 0 | 1010 | -3.51 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 0.2 | 12.8 | 86.9 | 0 | 0 | 1010 | 0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.2 | 2.5 | 16.4 | 80.9 | 0 | 0 | 1010 | -2.01 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.1 | 13.4 | 83.5 | 0 | 0 | 1010 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 16.4 | 83.6 | 0 | 0 | 1009 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.5 | 14.7 | 82.8 | 0 | 0 | 1009 | 0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-05-31
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: |  | OC
Instrument: | GA 2000 Plus
Serial No: | GA12599
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.9 | 22.1 | 76.9 | 0 | 0 | 1000 | 0.19 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.5 | 20.9 | 77.5 | 0 | 0 | 1000 | 0.21 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.4 | 22.8 | 76.7 | 0 | 0 | 1001 | 0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.2 | 0.2 | 20.7 | 78.9 | 0 | 0 | 1002 | 0.34 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 15.8 | 3.1 | 16.9 | 64.2 | 0 | 0 | 1000 | 0.95 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 5.8 | 2.9 | 18.8 | 72.5 | 0 | 0 | 1001 | 0.64 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.2 | 22.6 | 77 | 0 | 0 | 1000 | 0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 3.3 | 13.4 | 83.1 | 0 | 0 | 1000 | 0.74 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.2 | 5.5 | 4.1 | 90.2 | 0 | 0 | 1000 | 0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 0.5 | 22.5 | 76.8 | 0 | 0 | 1000 | 0.16 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 22.9 | 77 | 0 | 0 | 1000 | -0.36 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.4 | 22.2 | 77.3 | 0 | 0 | 999 | 0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 999 | -0.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 0 | 22.9 | 76.9 | 0 | 0 | 999 | 0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 7.4 | 2.9 | 89.6 | 0 | 0 | 1000 | -0.93 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.2 | 16.8 | 81.9 | 0 | 0 | 1000 | -0.45 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked |  |  |  | 100 | 0 | 0 |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.3 | 2.4 | 16.8 | 80.5 | 0 | 0 | 1000 | -1.23 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4 | 17.6 | 78.3 | 0 | 0 | 1000 | 0.25 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 1.3 | 22.3 | 76.3 | 0 | 0 | 999 | 0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 2.1 | 20.5 | 77.3 | 0 | 0 | 1000 | 0.26 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2018-05-16 22:53 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-05-15
Date of last factory calibration | 2018-05-03
Next service due | 2018-11-03
Date of last Gas Check | 2018-05-03
Security code | [4A331039]
ID | DATE | CH4 | CO2 | O2 | BALANCE | CH4 %LEL | PEAKCH4 | PEAKCO2 | MIN O2 | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | CHOSEN 3 | ANSWER 1 | ANSWER 2 | SITECHOSEN 1 | SITECHOSEN 2 | SITECHOSEN 3 | SITECHOSEN 4 | SITEANSWER 1
|  | % | % | % | % | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-05-16 10:26 | 46.5 | 32.9 | 1.7 | 18.9 | >>>> | 49.6 | 32.5 | 1.7 | 1014 | 196.29 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0035 | 2018-05-16 10:30 | 60.3 | 39.3 | 0.5 | 0 | >>>> | 63.6 | 40.1 | 0 | 1013 | 0.14 | 1 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0035 | 2018-05-16 10:31 | 61.3 | 39.3 | 0.4 | 0 | >>>> |  |  |  | 1013 | -5.04 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0036 | 2018-05-16 10:33 | 70.1 | 33.6 | 0 | 0 | >>>> | 70.1 | 39.2 | 0 | 1013 | -2.41 | 0 | 0 | LOW | closed | vacuum increased |  |  | 6 | drizzle | rain | overcast | light wind | 1 0
BHGV0036 | 2018-05-16 10:34 | 69.9 | 33.5 | 0 | 0 | >>>> |  |  |  | 1013 | -2.92 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0037 | 2018-05-16 10:38 | 32.4 | 30.4 | 1.3 | 35.9 | >>>> | 69.6 | 35.1 | 0 | 1013 | -3.37 | 0 | 0 | LOW | closed | no vacuum change |  |  | 6 | drizzle | rain | overcast | light wind | 1 0
BHM010MB | 2018-05-16 10:40 | 60.8 | 40.2 | 0.1 | 0 | >>>> | 62.1 | 40.1 | 0.1 | 1013 | -14.57 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0018 | 2018-05-16 10:41 | 60.6 | 40.6 | 0.1 | 0 | >>>> | 60.7 | 40.6 | 0.1 | 1014 | -14.93 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHLC004B | 2018-05-16 10:42 | 60.5 | 41.3 | 0 | 0 | >>>> |  |  |  | 1013 | 0 | 1 | 0 | LOW | closed | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0015 | 2018-05-16 10:44 | 59.6 | 41.2 | 0.3 | 0 | >>>> | 60.5 | 41.4 | 0.1 | 1013 | -14.86 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0014 | 2018-05-16 10:45 | 59.2 | 40.7 | 0.1 | 0 | >>>> | 59.7 | 41.4 | 0.1 | 1013 | -14.85 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0013 | 2018-05-16 10:46 | 0.4 | 8.2 | 14.2 | 77.2 | 8 | 59.4 | 40.9 | 0 | 1014 | 0 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0016 | 2018-05-16 10:49 | 51.6 | 35.5 | 2.3 | 10.6 | >>>> | 51.6 | 35.5 | 2.3 | 1014 | -0.02 | 1 | 0 | LOW | closed | vacuum increased |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0016 | 2018-05-16 10:50 | 52.2 | 36 | 2.3 | 9.5 | >>>> |  |  |  | 1014 | -14.22 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 7 | drizzle | rain | overcast | light wind | 1 0
BHPRL0C4 | 2018-05-16 10:52 | [8 empty] | 1013 | 0 | 0 | 0 | LOW |  |  |  | 34 |  | drizzle | rain | overcast | light wind | 1 0
BHL000C4 | 2018-05-16 10:55 | 21 | 18.7 | 6.4 | 53.9 | >>>> | 51.9 | 35.7 | 2.4 | 1013 | 0.02 | 48 | 0 | LOW | closed |  |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPRG017 | 2018-05-16 10:55 | [8 empty] | 1013 | 0.02 | 37 | 0 | LOW |  |  |  | 356 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0017 | 2018-05-16 10:58 | 65.7 | 37.8 | 0 | 0 | >>>> | 69.7 | 37.8 | 0 | 1013 | 6.36 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0017 | 2018-05-16 10:59 | 65.5 | 38.1 | 0.1 | 0 | >>>> |  |  |  | 1013 | -2.24 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 7 | drizzle | rain | overcast | light wind | 1 0
BHM010MA | 2018-05-16 11:01 | 61.4 | 38.9 | 0.1 | 0 | >>>> | 64.9 | 38.9 | 0.1 | 1014 | -14.86 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0038 | 2018-05-16 11:03 | 36.4 | 33.2 | 0.5 | 29.9 | >>>> | 60.9 | 40.1 | 0 | 1013 | -9.84 | 1 | 0 | LOW | partially open | vacuum decreased |  |  | 4 | drizzle | rain | overcast | light wind | 1 0
BHGV0038 | 2018-05-16 11:03 | 36.4 | 33.2 | 0.5 | 29.9 | >>>> |  |  |  | 1013 | -7.66 | 0 | 0 | LOW | closed | no vacuum change |  |  | 4 | drizzle | rain | overcast | light wind | 1 0
BHPRG039 | 2018-05-16 11:05 | [8 empty] | 1014 | 0.04 | 0 | 0 | LOW |  |  |  | 211 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0039 | 2018-05-16 11:08 | 1.7 | 3 | 16.1 | 79.2 | 34 | 37 | 33 | 0.6 | 1014 | 6.93 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0011 | 2018-05-16 11:15 | 28.7 | 27.3 | 2.3 | 41.7 | >>>> | 66.2 | 35.4 | 1.2 | 1014 | 0.06 | 0 | 0 | LOW | closed | no vacuum change |  |  | 4 | drizzle | rain | overcast | light wind | 1 0
BHGV0010 | 2018-05-16 11:15 | 52.5 | 32.2 | 2 | 13.3 | >>>> | 53.5 | 32.2 | 1.5 | 1014 | -10.25 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0040 | 2018-05-16 11:17 | 49.6 | 31.4 | 0.7 | 18.3 | >>>> | 53 | 31.2 | 0.7 | 1014 | -11.75 | 0 | 0 | LOW | partially open | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0040 | 2018-05-16 11:17 | 48.6 | 31.7 | 0.8 | 18.9 | >>>> |  |  |  | 1014 | -12.61 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHLC001B | 2018-05-16 11:18 | 0.8 | 9.7 | 13.6 | 75.9 | 16 | 48.4 | 31.7 | 1.1 | 1014 | -3.2 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0009 | 2018-05-16 11:19 | 52.2 | 31.4 | 0.3 | 16.1 | >>>> | 54.6 | 31.4 | 0.3 | 1014 | -13.09 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 7 | drizzle | rain | overcast | light wind | 1 0
BHLC0003 | 2018-05-16 11:22 | 4.1 | 8.5 | 14 | 73.4 | 82 | 50.4 | 32 | 0.9 | 1014 | -2.08 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPRL003 | 2018-05-16 11:22 | [8 empty] | 1014 | 0.07 | 0 | 0 | LOW |  |  |  | 951633 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0301 | 2018-05-16 11:25 | 14.3 | 10.8 | 11.5 | 63.4 | >>>> | 14.3 | 10.9 | 11.5 | 1014 | -14.01 | 0 | 0 | LOW | partially open | vacuum decreased |  |  |  | drizzle | rain | overcast | light wind | 1 0
BHGV0301 | 2018-05-16 11:26 | 14.3 | 10.9 | 11.5 | 63.3 | >>>> |  |  |  | 1014 | -9.5 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0012 | 2018-05-16 11:28 | 67 | 36.8 | 0.5 | 0 | >>>> | 71.7 | 36.5 | 0.5 | 1013 | -13.59 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR00003 | 2018-05-16 11:30 | 63.8 | 33.2 | 0.4 | 2.6 | >>>> | 65.1 | 38.1 | 0.1 | 1013 | -0.09 | 2 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR00003 | 2018-05-16 11:30 | 63.8 | 33.2 | 0.4 | 2.6 | >>>> |  |  |  | 1013 | -13.61 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 7 | drizzle | rain | overcast | light wind | 1 0
BHPRR003 | 2018-05-16 11:31 | [8 empty] | 1013 | 0 | 0 | 0 | LOW |  |  |  | 1382 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0046 | 2018-05-16 11:33 | 28.3 | 22.4 | 8.3 | 41 | >>>> | 63.8 | 33 | 0.6 | 1013 | -5.68 | 1 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPRG046 | 2018-05-16 11:34 | [8 empty] | 1013 | -0.06 | 1 | 0 | LOW | [5 empty] | drizzle | rain | overcast | light wind | 1 0
BHPRG046 | 2018-05-16 11:40 | 63.4 | 25.1 | 1.9 | 9.6 | >>>> | 63.2 | 25 | 1.9 | 1014 | -1.25 | 0 | 0 | LOW | closed | vacuum increased |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPRG046 | 2018-05-16 11:41 | 64.1 | 27.2 | 1 | 7.7 | >>>> | 65.3 | 27.2 | 1 | 1014 | -4.78 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRG042 | 2018-05-16 11:41 | 63.5 | 27 | 1 | 8.5 | >>>> |  |  |  | 1014 | -0.02 | 0 | 0 | LOW |  |  |  | 9457 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0043 | 2018-05-16 11:46 | 64.2 | 37.8 | 0.1 | 0 | >>>> | 68.8 | 37.8 | 0.1 | 1014 | -2.25 | 0 | 0 | LOW | closed | vacuum increased |  |  | 6 | drizzle | rain | overcast | light wind | 1 0
BHGV0043 | 2018-05-16 11:48 | 60 | 36.2 | 0.9 | 2.9 | >>>> | 64 | 38 | 0.2 | 1014 | -2.48 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0007 | 2018-05-16 11:54 | 58.4 | 32.7 | 0.3 | 8.6 | >>>> | 59.4 | 33.4 | 0.2 | 1014 | -3.21 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0008 | 2018-05-16 11:58 | 33 | 20.1 | 6.8 | 40.1 | >>>> |  |  |  | 1014 | -15.29 | 4 | 0 | LOW | closed | no vacuum change |  |  | 6 | drizzle | rain | overcast | light wind | 1 0
BHLC002R | 2018-05-16 11:59 | 63.2 | 31.6 | 0.2 | 5 | >>>> | 64 | 31.6 | 0.2 | 1014 | -15.17 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 7 | drizzle | rain | overcast | light wind | 1 0
BHGV0044 | 2018-05-16 12:01 | 56.6 | 29.9 | 0.3 | 13.2 | >>>> | 61.8 | 32.3 | 0.2 | 1014 | -1.18 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0044 | 2018-05-16 12:01 | 57.1 | 30.2 | 0.2 | 12.5 | >>>> |  |  |  | 1014 | -2.43 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRG044 | 2018-05-16 12:03 | 57.1 | 30.2 | 0.6 | 12.1 | >>>> |  |  |  | 1013 | -0.01 | 0 | 0 | LOW |  |  |  | 3089 |  | drizzle | rain | overcast | light wind | 1 0
BHR00001 | 2018-05-16 12:13 | 68.5 | 35.4 | 0 | 0 | >>>> | 69.2 | 35.4 | 0 | 1013 | 0.01 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0001 | 2018-05-16 12:17 | 67.8 | 35.8 | 0 | 0 | >>>> | 70.9 | 35.7 | 0 | 1013 | 0.06 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0045 | 2018-05-16 12:21 | 45.5 | 30.7 | 3.9 | 19.9 | >>>> | 67.4 | 35.8 | 0.2 | 1013 | -2.21 | 0 | 0 | LOW | closed | vacuum increased |  |  |  | drizzle | rain | overcast | light wind | 1 0
BHGV0045 | 2018-05-16 12:22 | 45.9 | 31 | 3.8 | 19.3 | >>>> |  |  |  | 1013 | -2.37 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0006 | 2018-05-16 12:26 | 0.1 | 6.1 | 15.4 | 78.4 | 2 | 46.1 | 30.9 | 4 | 1014 | -0.8 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0003 | 2018-05-16 12:28 | 74.6 | 29.2 | 0.4 | 0 | >>>> | 75.1 | 29.2 | 0.5 | 1014 | -13.78 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR0001B | 2018-05-16 12:28 | 72.1 | 30.9 | 1.3 | 0 | >>>> |  |  |  | 1014 | -0.08 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0004 | 2018-05-16 12:30 | 69.4 | 30.3 | 0.9 | 0 | >>>> | 71.7 | 30.9 | 0.8 | 1014 | 0.65 | 3 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0021 | 2018-05-16 12:46 | 40 | 25.6 | 2.1 | 31.4 | >>>> |  |  |  | 1014 | -4.5 | 3 | 0 | LOW | partially open | vacuum decreased |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHM050MB | 2018-05-16 12:59 | 56.4 | 34.9 | 0.5 | 8.2 | >>>> | 58.8 | 34.8 | 0.5 | 1013 | -13.25 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0025 | 2018-05-16 13:01 | 46.6 | 33 | 0 | 20.4 | >>>> | 54.9 | 35.5 | 0 | 1013 | -11.68 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV000A | 2018-05-16 13:02 | 23.6 | 19.5 | 7 | 49.9 | >>>> | 46.8 | 33 | 0.1 | 1013 | -11.35 | 9 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0024 | 2018-05-16 13:03 | 63.5 | 37.6 | 0.1 | 0 | >>>> | 66.2 | 37.6 | 0.1 | 1013 | -12.95 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0023 | 2018-05-16 13:05 | 0.1 | 9.2 | 12.3 | 78.4 | 2 | 62.7 | 38 | 0.1 | 1013 | -0.13 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0048 | 2018-05-16 13:11 | 49 | 35.7 | 2.3 | 13 | >>>> | 52.5 | 35.7 | 2.3 | 1013 | -13.04 | 2 | 0 | LOW | fully open | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0022 | 2018-05-16 13:12 | 49 | 35.5 | 2.4 | 13.1 | >>>> | 49.1 | 35.6 | 2.4 | 1013 | -0.01 | 2 | 0 | LOW | closed |  |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHM050MA | 2018-05-16 13:16 | 54.6 | 36.2 | 0.3 | 8.9 | >>>> | 56.2 | 36.2 | 0.3 | 1013 | -13.23 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRG048 | 2018-05-16 13:18 | 46.3 | 31 | 1.2 | 21.5 | >>>> |  |  |  | 1012 | -0.07 | 0 | 0 | LOW |  |  |  | 1827 |  | drizzle | rain | overcast | light wind | 1 0
BHLC0006 | 2018-05-16 13:21 | 13 | 22.1 | 6.5 | 58.4 | >>>> | 64 | 38.7 | 0 | 1012 | 0.41 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHLC006B | 2018-05-16 13:22 | 63.3 | 37.3 | 0.8 | 0 | >>>> | 66 | 36.9 | 0.8 | 1012 | -3.76 | 1 | 0 | LOW | partially open | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHLC006B | 2018-05-16 13:22 | 61.8 | 39.1 | 0.4 | 0 | >>>> |  |  |  | 1012 | -6.54 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRL06B | 2018-05-16 13:23 | 61.3 | 39.1 | 1 | 0 | >>>> |  |  |  | 1012 | -6.69 | 1 | 0 | LOW | [5 empty] | drizzle | rain | overcast | light wind | 1 0
BHPRL06B | 2018-05-16 13:23 | 61.3 | 39.1 | 1.8 | 0 | >>>> |  |  |  | 1012 | -6.98 | 1 | 0 | LOW |  |  |  | 29472 |  | drizzle | rain | overcast | light wind | 1 0
BHLC0005 | 2018-05-16 13:25 | 14.6 | 21.9 | 6.8 | 56.7 | >>>> | 60.7 | 39 | 0.7 | 1011 | -0.74 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0029 | 2018-05-16 13:26 | 61.8 | 36.5 | 0.4 | 1.3 | >>>> | 63.9 | 36.2 | 0.4 | 1011 | -12.6 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR00005 | 2018-05-16 13:28 | 0.8 | 8.9 | 14.2 | 76.1 | 16 | 60 | 38 | 0.4 | 1011 | -8.18 | 0 | 0 | LOW | partially open | vacuum decreased |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPRR005 | 2018-05-16 13:28 | 0.6 | 8 | 14.8 | 76.6 | 12 |  |  |  | 1011 | 0.05 | 0 | 0 | LOW |  |  |  | 434900 |  | drizzle | rain | overcast | light wind | 1 0
BHGV000C | 2018-05-16 13:30 | 67.6 | 35.4 | 0.7 | 0 | >>>> | 68.5 | 35 | 0.8 | 1011 | -7.38 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0028 | 2018-05-16 13:31 | 0.1 | 4.9 | 15.7 | 79.3 | 2 | 63.8 | 37.8 | 0.6 | 1012 | -6.94 | 0 | 0 | LOW | partially open | vacuum decreased |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGV0027 | 2018-05-16 13:33 | 66 | 34 | 0.3 | 0 | >>>> | 66.9 | 34 | 0.3 | 1012 | -11.5 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0026 | 2018-05-16 13:36 | 60.9 | 37.7 | 0 | 1.4 | >>>> | 61.4 | 37.6 | 0 | 1012 | -11.43 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV000B | 2018-05-16 13:46 | 52.1 | 36.8 | 0 | 11.1 | >>>> | 59.8 | 37.3 | 0 | 1011 | -10.82 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR0002B | 2018-05-16 13:46 | 52.1 | 36.8 | 0.1 | 11 | >>>> |  |  |  | 1011 | -13.84 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0030 | 2018-05-16 13:48 | 55.2 | 37.8 | 0 | 7 | >>>> | 55.2 | 37.8 | 0 | 1011 | -6 | 1 | 0 | LOW | partially open | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0030 | 2018-05-16 13:48 | 54.9 | 37.9 | 0 | 7.2 | >>>> |  |  |  | 1011 | -9.54 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0031 | 2018-05-16 13:50 | 54.4 | 38.3 | 0 | 7.3 | >>>> | 55 | 38.3 | 0 | 1011 | -10.26 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 8 | drizzle | rain | overcast | light wind | 1 0
BHGV0032 | 2018-05-16 13:54 | 60.3 | 42 | 0 | 0 | >>>> | 61.4 | 42 | 0 | 1011 | -2.84 | 2 | 0 | LOW | partially open | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0032 | 2018-05-16 13:54 | 59.5 | 42 | 0 | 0 | >>>> |  |  |  | 1011 | -2.94 | 2 | 0 | LOW | partially open | no vacuum change |  |  | 8 | drizzle | rain | overcast | light wind | 1 0
BHGV0033 | 2018-05-16 13:56 | 49.9 | 40.4 | 0.3 | 9.4 | >>>> | 59.5 | 42.2 | 0 | 1011 | -8.23 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR0006B | 2018-05-16 13:58 | 62.7 | 39.6 | 0 | 0 | >>>> | 62.7 | 39.6 | 0 | 1011 | 0.76 | 1 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHR0006B | 2018-05-16 13:58 | 62.6 | 40 | 0 | 0 | >>>> | 62.6 | 40.1 | 0 | 1011 | -1.29 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRR06B | 2018-05-16 13:59 | 62.3 | 40.1 | 0 | 0 | >>>> |  |  |  | 1011 | -0.24 | 1 | 0 | LOW |  |  |  | 394368 |  | drizzle | rain | overcast | light wind | 1 0
BHGV0049 | 2018-05-16 14:01 | 58.2 | 42.1 | 0.2 | 0 | >>>> | 62.3 | 42.1 | 0 | 1011 | -0.46 | 1 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHGV0049 | 2018-05-16 14:02 | 58.2 | 42.2 | 0.2 | 0 | >>>> |  |  |  | 1011 | -2.6 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPRG049 | 2018-05-16 14:02 | 58.1 | 42.2 | 0.2 | 0 | >>>> |  |  |  | 1011 | -0.18 | 1 | 0 | LOW |  |  |  | 58323 |  | drizzle | rain | overcast | light wind | 1 0
BHPW0005 | 2018-05-16 14:08 | 64.6 | 38.4 | 0 | 0 | >>>> | 69.4 | 38.4 | 0 | 1012 | -11.28 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPW0005 | 2018-05-16 14:09 | 63.9 | 38.5 | 0 | 0 | >>>> |  |  |  | 1012 | -10.95 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0
BHPW0004 | 2018-05-16 14:12 | 36.3 | 23.8 | 4.5 | 35.4 | >>>> | 65.1 | 38.3 | 0.1 | 1012 | -6.68 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPW0003 | 2018-05-16 14:16 | 1.3 | 7.6 | 14.6 | 76.5 | 26 | 30.4 | 25.9 | 5.8 | 1011 | -10.98 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHPW0001 | 2018-05-16 14:18 | 11.7 | 6.9 | 13.1 | 68.3 | >>>> | 21.9 | 9.6 | 12 | 1011 | -10.94 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2 | drizzle | rain | overcast | light wind | 1 0
BHGW0034 | 2018-05-16 14:21 | 21 | 11.9 | 4.2 | 62.9 | >>>> | 21 | 11.9 | 4.2 | 1012 | -0.48 | 4 | 0 | LOW | closed | no vacuum change |  |  | 4 | drizzle | rain | overcast | light wind | 1 0
BHG01MDA | 2018-05-16 14:28 | 52.7 | 35.6 | 0.4 | 11.3 | >>>> | 56.7 | 35.6 | 0.4 | 1011 | 198.92 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1 | drizzle | rain | overcast | light wind | 1 0

## June 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-06-07
Weather: | Sunny
Wind conditions: | Light Wind
Air Temperature: | 17 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.5 | 19.3 | 80.1 | 0 | 0 | 1001 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.1 | 17.5 | 80.3 | 0 | 0 | 1001 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.2 | 19.7 | 80 | 0 | 0 | 1003 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0 | 19.9 | 80 | 0 | 0 | 1002 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 11 | 3.2 | 18 | 67.8 | 0 | 0 | 1001 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.9 | 5 | 17 | 69.1 | 0 | 0 | 1002 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0 | 19.7 | 80.2 | 0 | 0 | 1001 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 3.8 | 2.1 | 94 | 0 | 0 | 1001 | 0.4 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 6.2 | 2.6 | 91.1 | 0 | 0 | 1001 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.2 | 19.3 | 80.4 | 0 | 0 | 1001 | -0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 19.6 | 80.2 | 0 | 0 | 1001 | -0.95 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 19.5 | 80.2 | 0 | 0 | 1001 | -0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 0.5 | 18.3 | 81 | 0 | 0 | 1001 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0 | 19.6 | 80.3 | 0 | 0 | 1001 | -0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 9.3 | 2.4 | 88.2 | 0 | 0 | 1001 | -0.8 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.3 | 11.6 | 87 | 0 | 0 | 1001 | 0.25 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.2 | 2.5 | 16.4 | 80.9 | 0 | 0 | 1001 | -2.41 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4.8 | 14.1 | 81 | 0 | 0 | 1001 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 19.5 | 80.3 | 0 | 0 | 1001 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 2.6 | 17.3 | 80 | 0 | 0 | 1001 | 0.44 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-06-14
Weather: | Overcast
Wind conditions: | Strong winds
Air Temperature: | 18 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.5 | 19.8 | 79.6 | 0 | 0 | 986 | 0.39 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0 | 20.2 | 79.7 | 0 | 0 | 986 | 0.18 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.5 | 20 | 79.4 | 0 | 0 | 988 | 0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0 | 20.2 | 79.7 | 0 | 0 | 988 | 0.13 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.3 | 0.9 | 19.6 | 78.2 | 0 | 0 | 988 | 0.1 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 7.2 | 4.3 | 17.9 | 70.6 | 0 | 0 | 988 | 0.13 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.1 | 20.1 | 79.7 | 0 | 0 | 988 | 0.58 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 3.5 | 14.1 | 82.3 | 0 | 0 | 988 | 0.39 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 5.6 | 3.7 | 90.6 | 0 | 0 | 988 | 0.14 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.2 | 19.9 | 79.8 | 0 | 0 | 989 | 0.1 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 20.1 | 79.7 | 0 | 0 | 989 | 0.12 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.5 | 19.5 | 79.9 | 0 | 0 | 988 | 0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.3 | 19.2 | 80.4 | 0 | 0 | 988 | 0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0 | 20 | 79.9 | 0 | 0 | 988 | 0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.4 | 9.3 | 2.7 | 87.6 | 0 | 0 | 985 | 0.17 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 0.6 | 12.9 | 86.4 | 0 | 0 | 985 | 0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.8 | 16 | 81.1 | 0 | 0 | 986 | -2.54 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4.9 | 15.7 | 79.3 | 0 | 0 | 985 | 0.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 20 | 79.8 | 0 | 0 | 986 | 0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 2.7 | 18.4 | 78.8 | 0 | 0 | 986 | 0.15 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-06-22
Weather: | Overcast
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 17.4 | 82.2 | 0 | 0 | 1015 | -0.1 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.8 | 15.8 | 82.4 | 0 | 0 | 1016 | -0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 1017 | -0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 17.6 | 82.4 | 0 | 0 | 1017 | -0.1 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.9 | 1.1 | 16.4 | 81.6 | 0 | 0 | 1016 | -0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.4 | 9.7 | 12.8 | 61.1 | 0 | 0 | 1016 | -0.12 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1016 | -1.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 4.6 | 94.1 | 0 | 0 | 1017 | -0.11 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.4 | 12.2 | 82.4 | 0 | 0 | 1017 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.7 | 16.7 | 81.6 | 0 | 0 | 1017 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 17.7 | 82.3 | 0 | 0 | 1016 | -0.12 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1016 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.1 | 17.5 | 82.3 | 0 | 0 | 1017 | -0.15 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 17.7 | 82.1 | 0 | 0 | 1016 | -0.1 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 1015 | -0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.5 | 11.1 | 88.4 | 0 | 0 | 1015 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.6 | 16.2 | 81.1 | 0 | 0 | 1015 | -2.41 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.5 | 15.2 | 80.3 | 0 | 0 | 1015 | -0.1 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 17.4 | 82.4 | 0 | 0 | 1015 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 16.6 | 81.3 | 0 | 0 | 1015 | -0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-06-26
Weather: | Overcast
Wind conditions: | Calm
Air Temperature: | 21 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 17.2 | 82.4 | 0 | 0 | 1015 | -0.24 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.6 | 15.9 | 82.5 | 0 | 0 | 1016 | -0.18 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 1017 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 17.4 | 82.6 | 0 | 0 | 1017 | -0.11 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.1 | 1.6 | 16.3 | 81 | 0 | 0 | 1016 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 20.2 | 10.2 | 12.1 | 57.5 | 0 | 0 | 1016 | -0.15 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0 | 17.4 | 82.6 | 0 | 0 | 1016 | -0.45 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 4.3 | 94.2 | 0 | 0 | 1017 | -0.33 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.7 | 11.7 | 82.6 | 0 | 0 | 1017 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1 | 17.3 | 81.7 | 0 | 0 | 1017 | -0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 1016 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 17.3 | 82.6 | 0 | 0 | 1016 | -0.13 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 1016 | -0.16 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.3 | 82.7 | 0 | 0 | 1017 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 17.3 | 82.7 | 0 | 0 | 1015 | -0.41 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.4 | 11.3 | 88.3 | 0 | 0 | 1015 | -0.22 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.4 | 16.5 | 81 | 0 | 0 | 1017 | -2.54 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.8 | 14.9 | 80.3 | 0 | 0 | 1015 | -0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 1015 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.3 | 16.3 | 81.4 | 0 | 0 | 1015 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2018-06-14 19:21 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-06-04
Date of last factory calibration | 2018-05-03
Next service due | 2018-11-03
Date of last Gas Check | 2018-05-03
Security code | [271D1600]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | SITECHOSEN 1 | SITECHOSEN 2 | SITECHOSEN 3 | SITEANSWER 1
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-06-14 09:49 | 57.1 | 39.6 | 0.6 | 2.7 | 988 | 195.09 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0035 | 2018-06-14 09:53 | 60.7 | 44.4 | 0.2 | 0 | 987 | -1.16 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0035 | 2018-06-14 09:54 | 60.6 | 44.5 | 0.3 | 0 | 987 | -1.35 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0036 | 2018-06-14 09:56 | 70.1 | 36.2 | 0.1 | 0 | 987 | -1.2 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0037 | 2018-06-14 09:59 | 66.9 | 37.6 | 0.2 | 0 | 987 | -0.62 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0037 | 2018-06-14 10:00 | 66.9 | 37.6 | 0.3 | 0 | 987 | -0.87 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHM010MB | 2018-06-14 10:02 | 62.7 | 39.6 | 0.2 | 0 | 987 | -8.83 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0018 | 2018-06-14 10:03 | 60.7 | 44.6 | 0 | 0 | 987 | -8.62 | 1 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC004B | 2018-06-14 10:03 |  |  |  |  | 987 | 0.24 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR0004B | 2018-06-14 10:04 |  |  |  |  | 987 | 0.01 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0015 | 2018-06-14 10:05 | 60.3 | 44.8 | 0.1 | 0 | 987 | -8.47 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0014 | 2018-06-14 10:06 | 61.2 | 43.4 | 0 | 0 | 987 | -8.68 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0013 | 2018-06-14 10:07 | 0.6 | 10 | 14.6 | 74.8 | 987 | 0.05 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0016 | 2018-06-14 10:08 |  |  |  |  | 987 | -2.36 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHL000C4 | 2018-06-14 10:10 | 64.4 | 37.3 | 0.1 | 0 | 987 | -0.6 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0017 | 2018-06-14 10:17 |  |  |  |  | 986 | 147.18 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHM010MA | 2018-06-14 10:20 | 60.7 | 42 | 0.3 | 0 | 987 | -9.64 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0038 | 2018-06-14 10:24 | 61.2 | 36.2 | 1.3 | 1.3 | 987 | -1.36 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0039 | 2018-06-14 10:26 | 32.8 | 17.5 | 4.7 | 45 | 988 | -0.61 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0011 | 2018-06-14 10:31 | 33.3 | 32.2 | 1 | 33.5 | 988 | -0.5 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0010 | 2018-06-14 10:36 | 54.5 | 32.2 | 0.4 | 12.9 | 989 | -0.07 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0040 | 2018-06-14 10:43 | 57.5 | 33.3 | 0.7 | 8.5 | 989 | -8.14 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0040 | 2018-06-14 10:43 | 56.6 | 34.9 | 0.6 | 7.9 | 989 | -9.55 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC001B | 2018-06-14 10:44 | 0.4 | 6.4 | 17.8 | 75.4 | 989 | -2.02 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0009 | 2018-06-14 10:45 | 62.4 | 32.2 | 0.5 | 4.9 | 989 | -9.1 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC0003 | 2018-06-14 10:51 | 35.9 | 28.2 | 5.7 | 30.2 | 989 | -0.7 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0301 | 2018-06-14 10:53 | 26.9 | 26.3 | 4.9 | 41.9 | 988 | -1.06 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0012 | 2018-06-14 10:56 | 62.8 | 42.5 | 0.2 | 0 | 988 | -7.97 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR00003 | 2018-06-14 10:58 | 1.8 | 3.8 | 17.8 | 76.6 | 987 | -7.89 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR00003 | 2018-06-14 10:58 | 2 | 3.8 | 17 | 77.2 | 987 | 0.02 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0046 | 2018-06-14 11:01 | 59.6 | 45.3 | 0 | 0 | 987 | -0.83 | 1 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0046 | 2018-06-14 11:01 | 59.5 | 45.5 | 0.2 | 0 | 987 | -4.84 | 1 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0041 | 2018-06-14 11:02 |  |  |  |  | 987 | -0.18 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0042 | 2018-06-14 11:06 | 48.5 | 23.6 | 5.3 | 22.6 | 987 | -1.78 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0042 | 2018-06-14 11:06 | 48.6 | 23.4 | 5.3 | 22.7 | 987 | -0.06 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0043 | 2018-06-14 11:09 | 65.1 | 37.6 | 0.6 | 0 | 989 | -2.09 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0007 | 2018-06-14 11:12 | 65.2 | 35.9 | 0.4 | 0 | 989 | -2.8 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0008 | 2018-06-14 11:14 | 15.2 | 11.9 | 13.3 | 59.6 | 989 | 11.1 | 8 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC002R | 2018-06-14 11:15 | 62.7 | 34.2 | 0.1 | 3 | 989 | -8.69 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0044 | 2018-06-14 11:16 | 48.8 | 27.7 | 3.2 | 20.3 | 989 | 0.22 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR00001 | 2018-06-14 11:21 | 58.2 | 34.7 | 1.8 | 5.3 | 989 | -8.27 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0001 | 2018-06-14 11:22 | 62.5 | 35.4 | 1 | 1.1 | 988 | -2.67 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0001 | 2018-06-14 11:22 | 62.3 | 37.3 | 0.9 | 0 | 988 | -4.91 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0045 | 2018-06-14 11:24 | 56.1 | 36.9 | 0.3 | 6.7 | 988 | -6.14 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0045 | 2018-06-14 11:24 | 56.4 | 36.9 | 0.3 | 6.4 | 988 | -7.51 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0006 | 2018-06-14 11:28 | 0.6 | 7.9 | 16.8 | 74.7 | 989 | -0.1 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0003 | 2018-06-14 11:30 | 70.8 | 35.9 | 0 | 0 | 989 | -8.18 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR0001B | 2018-06-14 11:32 | 63.3 | 38.8 | 0.5 | 0 | 989 | -7.46 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0004 | 2018-06-14 11:33 | 71.3 | 32.6 | 0.7 | 0 | 989 | -3.89 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0004 | 2018-06-14 11:34 | 71.4 | 32.5 | 0.7 | 0 | 989 | -5.71 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC002B | 2018-06-14 11:39 | 9.2 | 7.8 | 16.3 | 66.7 | 988 | -1.02 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0021 | 2018-06-14 11:41 | 64.4 | 41.3 | 0.1 | 0 | 988 | -1.6 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0026 | 2018-06-14 11:50 | 61.6 | 40.5 | 0.2 | 0 | 988 | -7.52 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0047 | 2018-06-14 11:51 | 26.9 | 20.7 | 5.4 | 47 | 989 | -0.48 | 7 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHM050MB | 2018-06-14 11:59 | 53.3 | 37.6 | 1.7 | 7.4 | 990 | -8.61 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0025 | 2018-06-14 12:01 | 53 | 35.5 | 0.2 | 11.3 | 990 | -3.94 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV000A | 2018-06-14 12:02 | 29.4 | 22.5 | 5.5 | 42.6 | 990 | 0.85 | 18 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0024 | 2018-06-14 12:04 | 65.3 | 38.5 | 0.1 | 0 | 990 | -8.71 | 3 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0023 | 2018-06-14 12:05 | 2.3 | 14.2 | 12.8 | 70.7 | 990 | -2.07 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0022 | 2018-06-14 12:07 |  |  |  |  | 990 | -0.07 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0048 | 2018-06-14 12:08 | 47.5 | 33.6 | 3.8 | 15.1 | 990 | -8.72 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHM050MA | 2018-06-14 12:10 | 56.6 | 37.7 | 1.7 | 4 | 990 | -9.09 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC0006 | 2018-06-14 12:12 | 12.8 | 19 | 8.6 | 59.6 | 990 | -0.15 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC006B | 2018-06-14 12:15 | 64.3 | 42.3 | 0.2 | 0 | 989 | -2.96 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR0006B | 2018-06-14 12:16 | 54.8 | 42.2 | 0.9 | 2.1 | 989 | -4.59 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHLC0005 | 2018-06-14 12:17 | 0.5 | 7.6 | 17.6 | 74.3 | 989 | -0.23 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0029 | 2018-06-14 12:18 | 66.8 | 37.5 | 0.3 | 0 | 989 | -7.87 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV000C | 2018-06-14 12:19 | 61.9 | 40.3 | 0.1 | 0 | 989 | -6.59 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0028 | 2018-06-14 12:21 | 6.4 | 9.4 | 16.8 | 67.4 | 989 | -5.33 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0027 | 2018-06-14 12:23 | 65 | 40.8 | 0.1 | 0 | 989 | -7.96 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR0002B | 2018-06-14 12:25 | 63.9 | 41.5 | 0.2 | 0 | 990 | -8.12 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV000B | 2018-06-14 12:28 | 63.1 | 41.5 | 1.7 | 0 | 990 | -6.42 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0030 | 2018-06-14 12:31 | 61.7 | 41.1 | 0.1 | 0 | 989 | -7.48 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHR00005 | 2018-06-14 12:34 | 0.8 | 8.9 | 14.2 | 76.1 | 990 | -0.04 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0031 | 2018-06-14 12:39 | 54.4 | 38.3 | 0 | 7.3 | 990 | -7.99 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0032 | 2018-06-14 12:43 | 60.3 | 42 | 0 | 0 | 990 | -8.14 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0033 | 2018-06-14 12:46 | 51.2 | 40 | 0.2 | 8.6 | 990 | -6.98 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0049 | 2018-06-14 12:48 | 55.9 | 41.6 | 1.2 | 1.3 | 990 | -0.91 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGV0049 | 2018-06-14 12:49 | 56.3 | 42.9 | 0.7 | 0.1 | 990 | -2.56 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0006 | 2018-06-14 12:53 | 4.5 | 17 | 11.9 | 66.6 | 991 | -0.12 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0005 | 2018-06-14 12:55 | 64.4 | 34.4 | 0.4 | 0.8 | 991 | -8.45 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0004 | 2018-06-14 12:58 | 4.2 | 10.5 | 15.2 | 70.1 | 991 | -0.07 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0003 | 2018-06-14 13:01 | 6.3 | 12 | 14 | 67.7 | 991 | -8.3 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0002 | 2018-06-14 13:03 | 5 | 10.9 | 13.6 | 70.5 | 991 | -0.01 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHPW0001 | 2018-06-14 13:05 | 7.3 | 6.3 | 16.7 | 69.7 | 991 | -8.45 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHGW0034 | 2018-06-14 13:10 | 37.1 | 17.9 | 5.6 | 39.4 | 992 | -0.38 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0
BHG01MDA | 2018-06-14 13:15 | 58.2 | 38.4 | 0.5 | 2.9 | 992 | 197.5 | 0 | 0 | LOW | overcast | sunny | strong wind | 1 0

## July 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-07-04
Weather: | Overcast
Wind conditions: | Calm
Air Temperature: | 18 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 17.8 | 81.7 | 0 | 0 | 1007 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2 | 15.4 | 82.6 | 0 | 1 | 1006 | -0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.8 | 16.8 | 82.4 | 0 | 0 | 1008 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.8 | 17.4 | 81.8 | 0 | 0 | 1007 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.3 | 3.1 | 13.6 | 79 | 0 | 0 | 1008 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22.8 | 10.3 | 11.8 | 55.1 | 0 | 1 | 1007 | -0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 1009 | -0.06 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2 | 4.7 | 93.3 | 0 | 0 | 1008 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.9 | 12.6 | 81.5 | 0 | 0 | 1008 | -0.13 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 17.4 | 81.2 | 0 | 0 | 1007 | 0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1008 | 0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 2.3 | 16.8 | 80.9 | 0 | 1 | 1008 | -0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0 | 16.9 | 83.1 | 0 | 0 | 1008 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 1008 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1008 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.6 | 10.6 | 88.8 | 0 | 0 | 1008 | 0.07 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.2 | 16.1 | 81.6 | 0 | 0 | 1008 | -2.32 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.4 | 14.6 | 81 | 0 | 1 | 1007 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 1008 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 3.1 | 16.5 | 80.4 | 0 | 0 | 1007 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-07-12
Weather: | Overcast
Wind conditions: | Calm
Air Temperature: | 18 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 1 | 1007 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 15.7 | 82.1 | 0 | 0 | 1005 | 0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.1 | 16.2 | 82.7 | 0 | 0 | 1006 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 16.8 | 81.9 | 0 | 1 | 1006 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.5 | 3.5 | 12.7 | 77.3 | 0 | 0 | 1006 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 24.3 | 10.1 | 11.3 | 54.3 | 0 | 1 | 1006 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.8 | 16.9 | 82.3 | 0 | 1 | 1007 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 5.3 | 93.2 | 0 | 0 | 1006 | -0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.1 | 13.2 | 81.7 | 0 | 0 | 1006 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1 | 17.3 | 81.7 | 0 | 1 | 1005 | 0.08 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 18.1 | 81.5 | 0 | 1 | 1006 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 2.8 | 15.9 | 81.3 | 0 | 1 | 1005 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 1006 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.8 | 82.2 | 0 | 0 | 1006 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 1 | 1006 | -0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.4 | 10 | 89.6 | 0 | 0 | 1006 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.1 | 16.4 | 81.4 | 0 | 0 | 1008 | -2.32 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.9 | 14.1 | 81 | 0 | 0 | 1006 | 0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 16.5 | 83.1 | 0 | 0 | 1005 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 3 | 16.2 | 80.8 | 0 | 1 | 1006 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 1 | 1016 | 0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.8 | 16.1 | 82.1 | 0 | 0 | 1018 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 15.7 | 82.9 | 0 | 1 | 1017 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 2.5 | 16.5 | 81 | 0 | 0 | 1017 | 0.1 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.6 | 3.4 | 12.9 | 75.1 | 0 | 1 | 1017 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22.9 | 10.3 | 12.1 | 54.7 | 0 | 0 | 1018 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 16.2 | 82.5 | 0 | 0 | 1017 | 0.08 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 14.9 | 83.7 | 0 | 0 | 1017 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.5 | 14.8 | 80.7 | 0 | 0 | 1016 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.9 | 17.3 | 80.8 | 0 | 0 | 1017 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 17.4 | 82.1 | 0 | 0 | 1017 | 0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 2.9 | 16.5 | 80.6 | 0 | 2 | 1017 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 1 | 1017 | -0.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1017 | 0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 17.1 | 82.7 | 0 | 2 | 1017 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 10.6 | 89.1 | 0 | 1 | 1017 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.4 | 15.9 | 81.6 | 0 | 0 | 1017 | -2.35 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.4 | 14.3 | 80.3 | 0 | 0 | 1016 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 15.9 | 83.4 | 0 | 1 | 1017 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 3.7 | 16.4 | 79.9 | 0 | 0 | 1017 | 0.12 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2018-07-06 17:30 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-07-02
Date of last factory calibration | 2018-05-03
Next service due | 2018-11-03
Date of last Gas Check | 2018-05-03
Security code | [3E5D2D5E]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | CHOSEN 3 | ANSWER 1 | ANSWER 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-07-06 07:37 | 48.5 | 34.7 | 1.7 | 15.1 | 1004 | 197.89 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV0035 | 2018-07-06 07:41 | 59.6 | 40.2 | 0.6 | 0 | 1004 | -1.52 | 0 | 0 | LOW | partially open | vacuum increased |  |  | 1
BHGV0035 | 2018-07-06 07:42 | 58.5 | 40.4 | 0.8 | 0.3 | 1004 | -2.04 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0036 | 2018-07-06 07:43 | 47.7 | 33.2 | 0.1 | 19 | 1004 | -0.59 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0037 | 2018-07-06 07:46 | 39.2 | 25.6 | 2.8 | 32.4 | 1004 | 0.4 | 0 | 0 | LOW | closed | no vacuum change |  |  | 4
BHM010MB | 2018-07-06 07:48 | 55.8 | 38.5 | 1.7 | 4 | 1004 | -6.84 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 2
BHGV0018 | 2018-07-06 07:49 | 60 | 41.4 | 0.2 | 0 | 1004 | -6.71 | 1 | 0 | LOW | fully open |  |  |  | 1
BHLC004B | 2018-07-06 07:49 |  |  |  |  | 1004 | 0.15 | 1 | 0 | LOW | closed | no vacuum change |  |  | 8
BHR0004B | 2018-07-06 07:51 | 61.6 | 38.2 | 0.3 | 0 | 1004 | 109.54 | 1 | 0 | LOW | closed | vacuum increased |  |  | 8
BHGV0015 | 2018-07-06 07:53 | 60.1 | 41.3 | 0.4 | 0 | 1004 | -6.82 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV0014 | 2018-07-06 07:54 | 59.1 | 41.4 | 0.1 | 0 | 1004 | -6.86 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV0013 | 2018-07-06 07:55 | 2.6 | 14.5 | 15.4 | 67.5 | 1004 | 0.08 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHGV0016 | 2018-07-06 07:56 | 22.1 | 14.4 | 14.2 | 49.3 | 1004 | 0.16 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHL000C4 | 2018-07-06 07:58 | 59.8 | 36.6 | 0.1 | 3.5 | 1004 | 0.14 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 8
BHPRL0C4 | 2018-07-06 07:59 | 59.6 | 36.7 | 0.8 | 2.9 | 1003 | 0.06 | 0 | 0 | LOW |  |  |  | 41
BHGV0017 | 2018-07-06 08:01 | 60 | 34.9 | 0.8 | 4.3 | 1003 | 103.05 | 2 | 0 | LOW | fully open | no vacuum change |  |  | 8
BHPRG017 | 2018-07-06 08:02 | 60.1 | 35.2 | 1 | 3.7 | 1003 | 0.06 | 1 | 0 | LOW |  |  |  | 64203
BHM010MA | 2018-07-06 08:04 | 56.1 | 40.4 | 1 | 2.5 | 1003 | -6.99 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 2
BHGV0038 | 2018-07-06 08:06 | 62.8 | 39.1 | 0.4 | 0 | 1004 | -0.88 | 0 | 0 | LOW | partially open | vacuum increased |  |  | 1
BHGV0038 | 2018-07-06 08:06 | 63 | 38.4 | 0.5 | 0 | 1004 | -1.33 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHR00003 | 2018-07-06 08:09 | 43.2 | 27.8 | 5.9 | 23.1 | 1003 | -3.72 | 3 | 0 | LOW | closed | no vacuum change |  |  | 2
BHPRL003 | 2018-07-06 08:10 | 43.4 | 27.8 | 5.7 | 23.1 | 1003 | 0.2 | 3 | 0 | LOW |  |  |  | 63764
BHGV0011 | 2018-07-06 08:12 | 51.5 | 35 | 0.8 | 12.7 | 1004 | -1.98 | 0 | 0 | LOW | closed | vacuum increased |  |  | 2
BHGV0011 | 2018-07-06 08:12 | 51.8 | 35.4 | 0.7 | 12.1 | 1004 | -2.33 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0039 | 2018-07-06 08:14 | 31.4 | 20.7 | 8.2 | 39.7 | 1004 | -1.29 | 0 | 0 | LOW | closed | no vacuum change |  |  | 6
BHPRG039 | 2018-07-06 08:15 | 31.7 | 20.4 | 8 | 39.9 | 1004 | 0.21 | 0 | 0 | LOW |  |  |  | 9704
BHGV0010 | 2018-07-06 08:19 |  |  |  |  | 1004 | 0.09 | 0 | 0 | LOW | closed | no vacuum change |  |  | 8
BHGV0040 | 2018-07-06 08:21 | 55.1 | 33.7 | 1.2 | 10 | 1004 | -4.66 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 2
BHLC001B | 2018-07-06 08:22 | 0.3 | 5.5 | 20.7 | 73.5 | 1004 | -2.59 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHGV0009 | 2018-07-06 08:23 | 58.3 | 33.1 | 1.2 | 7.4 | 1004 | -6.42 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 2
BHGV0301 | 2018-07-06 08:27 | 62.4 | 41 | 0 | 0 | 1004 | 0.21 | 0 | 0 | LOW | closed | vacuum increased |  |  | 1
BHGV0301 | 2018-07-06 08:28 | 61.9 | 41 | 0.4 | 0 | 1004 | -0.71 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0012 | 2018-07-06 08:31 | 59.2 | 43.3 | 0.1 | 0 | 1003 | -4.53 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHR00003 | 2018-07-06 08:33 | 64.9 | 38.4 | 0 | 0 | 1002 | 0.79 | 1 | 0 | LOW | closed | vacuum increased |  |  | 1
BHR00003 | 2018-07-06 08:34 | 65.1 | 38.3 | 0 | 0 | 1002 | -3.31 | 1 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHPRR003 | 2018-07-06 08:34 | 64.8 | 38.2 | 0 | 0 | 1002 | -2.07 | 1 | 0 | LOW |  |  |  | 9215
BHGV0046 | 2018-07-06 08:36 | 39.8 | 31.4 | 6.3 | 22.5 | 1002 | -0.82 | 0 | 0 | LOW | partially open | vacuum decreased |  |  | 2
BHGV0046 | 2018-07-06 08:37 | 39.9 | 31.4 | 6.2 | 22.5 | 1002 | 0.16 | 0 | 0 | LOW | closed | no vacuum change |  |  | 8
BHPRG041 | 2018-07-06 08:37 | 40.1 | 31.4 | 5.7 | 22.8 | 1002 | 0.13 | 0 | 0 | LOW |  |  |  | 184888
BHPRG046 | 2018-07-06 08:38 | 40.2 | 31.4 | 5.6 | 22.8 | 1002 | 0.13 | 0 | 0 | LOW |  |  |  | 18650
BHGV0044 | 2018-07-06 08:43 | 13.8 | 21.4 | 3.1 | 61.7 | 1003 | -4.36 | 0 | 0 | LOW | partially open | vacuum decreased |  |  | 4
BHGV0044 | 2018-07-06 08:43 | 14 | 21.3 | 3.1 | 61.6 | 1003 | -0.05 | 0 | 0 | LOW | closed | no vacuum change |  |  | 4
BHPRG044 | 2018-07-06 08:44 | 14.1 | 21.3 | 3.3 | 61.3 | 1003 | 0.11 | 0 | 0 | LOW |  |  |  | 22310
BHR00001 | 2018-07-06 08:46 | 39.6 | 28.3 | 2 | 30.1 | 1003 | -6.52 | 0 | 0 | LOW | fully open | vacuum decreased |  |  | 4
BHR00001 | 2018-07-06 08:46 | 39.8 | 29 | 2 | 29.2 | 1003 | -3.34 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 4
BHR0001B | 2018-07-06 08:47 | 57.4 | 34.9 | 0.8 | 6.9 | 1002 | -2.92 | 0 | 0 | LOW | partially open | vacuum increased |  |  | 1
BHR0001B | 2018-07-06 08:47 | 57.4 | 35.4 | 0.7 | 6.5 | 1002 | -4.58 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHPRG045 | 2018-07-06 08:50 | 56 | 35.2 | 1.2 | 7.6 | 1002 | 0.1 | 0 | 0 | LOW |  |  |  | 17760
BHGV0045 | 2018-07-06 08:52 | 46.7 | 31.2 | 0.8 | 21.3 | 1002 | -6.32 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 4
BHLC002B | 2018-07-06 08:56 | 27.6 | 21.8 | 10.7 | 39.9 | <<<< | 0 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHGV0026 | 2018-07-06 09:00 | 63.8 | 36.7 | 0.2 | 0 | 1002 | -4.7 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHR0002B | 2018-07-06 09:03 | 66.5 | 36.6 | 0.1 | 0 | 1002 | -4.34 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV000B | 2018-07-06 09:06 | 53.5 | 37.7 | 0 | 8.8 | 1001 | -5.82 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV0028 | 2018-07-06 09:10 | 3.1 | 5.4 | 18.7 | 72.8 | 1001 | -2.79 | 0 | 0 | LOW | closed | no vacuum change |  |  | 4
BHGV000C | 2018-07-06 09:12 | 66.5 | 36.3 | 0.4 | 0 | 1001 | -3.58 | 1 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHGV0029 | 2018-07-06 09:13 | 60.2 | 39.1 | 0.1 | 0.6 | 1001 | -6.57 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1
BHR00005 | 2018-07-06 09:14 | 35.9 | 30 | 3.8 | 30.3 | 1001 | 0.07 | 0 | 0 | LOW | closed | no vacuum change |  |  | 8
BHPRR005 | 2018-07-06 09:15 | 34.2 | 28.5 | 4.5 | 32.8 | 1001 | 0.04 | 0 | 0 | LOW |  |  |  | 434900
BHLC0005 | 2018-07-06 09:17 | 3.2 | 13.4 | 15.7 | 67.7 | 1001 | 0.02 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHLC0006 | 2018-07-06 09:19 | 0.1 | 2.9 | 20.2 | 76.8 | 1002 | 0.08 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHLC006B | 2018-07-06 09:20 | 48.8 | 33.6 | 2.7 | 14.9 | 1001 | -3.81 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 2
BHPRL06B | 2018-07-06 09:21 | 47 | 34 | 3.4 | 15.6 | 1001 | -0.09 | 0 | 0 | LOW |  |  |  | 29644
BHR0006B | 2018-07-06 09:22 | 60.6 | 42.3 | 0.1 | 0 | 1001 | -1.79 | 0 | 0 | LOW | partially open | vacuum increased |  |  | 1
BHR0006B | 2018-07-06 09:23 | 59.5 | 43.2 | 0.7 | 0 | 1001 | -3.27 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0033 | 2018-07-06 09:24 | 47.7 | 38.1 | 0.2 | 14 | 1001 | -5.51 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHGV0049 | 2018-07-06 09:26 | 59.1 | 41.2 | 0.4 | 0 | 1001 | -0.82 | 0 | 0 | LOW | partially open | no vacuum change |  |  | 1
BHPRG049 | 2018-07-06 09:26 | 59.3 | 41.4 | 0.4 | 0 | 1001 | -1.77 | 0 | 0 | LOW |  |  |  | 196126
BHGW0034 | 2018-07-06 09:30 | 32.6 | 30.1 | 6.2 | 31.1 | 1002 | 0.07 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHPW0001 | 2018-07-06 09:31 | 7.7 | 8.4 | 16.1 | 67.8 | 1002 | -5.41 | 0 | 0 | LOW | closed | no vacuum change |  |  | 2
BHG01MDA | 2018-07-06 09:33 | 53.7 | 36.7 | 0.4 | 9.2 | 1002 | 193.57 | 0 | 0 | LOW | fully open | no vacuum change |  |  | 1

## August 2018
Date | 2018-08-01
Weather: | Overcast
Wind conditions: | Light Wind
Air Temperature: | 21 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 16.8 | 82.7 | 0 | 0 | 1002 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.4 | 15.1 | 82.4 | 0 | 0 | 1003 | -0.55 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 | Flooded | [8 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 1.2 | 16 | 82.7 | 0 | 0 | 1003 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 2.3 | 16.5 | 81.2 | 0 | 0 | 1002 | 0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.1 | 3.4 | 13.4 | 79.1 | 0 | 0 | 1002 | 0.39 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.1 | 8.3 | 13.1 | 64.5 | 0 | 0 | 1002 | -0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.2 | 82.4 | 0 | 0 | 1002 | 0.09 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.5 | 15.8 | 81.6 | 0 | 0 | 1003 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 4.5 | 13.9 | 81.5 | 0 | 0 | 1003 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 4.2 | 14.5 | 81.2 | 0 | 0 | 1002 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.1 | 82.8 | 0 | 0 | 1002 | -0.77 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.4 | 16.7 | 82.8 | 0 | 0 | 1002 | -0.41 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0 | 17.2 | 82.7 | 0 | 0 | 1002 | -0.13 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.2 | 82.8 | 0 | 0 | 1001 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 4.4 | 9.1 | 86.4 | 0 | 0 | 1002 | -2.44 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.8 | 10.4 | 87.7 | 0 | 0 | 1002 | 0.68 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 6.7 | 9.7 | 83.5 | 0 | 0 | 1002 | 0.42 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4 | 13.5 | 82.4 | 0 | 0 | 1002 | 0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 1002 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.3 | 16.2 | 82.4 | 0 | 0 | 1002 | 0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2018-08-08
Weather: | Overcast
Wind conditions: | Light Wind
Air Temperature: | 19 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 17 | 82.5 | 0 | 0 | 993 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.3 | 16 | 81.7 | 0 | 0 | 993 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 17 | 82.5 | 0 | 0 | 994 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 16.2 | 82.4 | 0 | 0 | 994 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.8 | 17.4 | 81.8 | 0 | 0 | 993 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.7 | 3.2 | 15.7 | 73.4 | 0 | 0 | 993 | 0 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.8 | 6.6 | 14.4 | 68.2 | 0 | 0 | 993 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 993 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.3 | 16.2 | 81.4 | 0 | 0 | 993 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 4.5 | 14.6 | 80.8 | 0 | 0 | 993 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 4.1 | 15 | 80.8 | 0 | 0 | 993 | 0 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 993 | -0.38 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 17.1 | 82.6 | 0 | 0 | 993 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 16.3 | 82.5 | 0 | 0 | 992 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.4 | 82.6 | 0 | 0 | 992 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.8 | 5.5 | 89.7 | 0 | 0 | 993 | -0.62 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 2 | 11.4 | 86.3 | 0 | 0 | 993 | -0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 7.9 | 9.4 | 82.7 | 0 | 0 | 993 | -0.45 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.4 | 14.2 | 81.4 | 0 | 0 | 993 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 992 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 16.5 | 82.2 | 0 | 0 | 992 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2018-08-14
Weather: | Overcast
Wind conditions: | Calm
Air Temperature: | 19 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 998 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 15.1 | 82.7 | 0 | 0 | 999 | -0.11 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 | Flooded | [8 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 0 | 1000 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.3 | 15.8 | 82.9 | 0 | 0 | 1000 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 1 | 998 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.1 | 1.8 | 14.2 | 81.9 | 0 | 0 | 999 | -0.4 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22 | 9.9 | 11.5 | 56.6 | 0 | 1 | 999 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1 | 16.8 | 82.2 | 0 | 1 | 998 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.6 | 16 | 82.4 | 0 | 0 | 999 | -0.1 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.8 | 14.6 | 82.6 | 0 | 0 | 998 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.4 | 15.2 | 82.4 | 0 | 0 | 999 | 0.32 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.4 | 16.6 | 82 | 0 | 0 | 999 | -1.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 999 | 0 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.7 | 16.8 | 82.5 | 0 | 0 | 999 | -0.13 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.6 | 16.8 | 82.6 | 0 | 0 | 999 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.1 | 9.6 | 86.3 | 0 | 0 | 999 | -0.28 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 3.4 | 13.8 | 82.8 | 0 | 0 | 998 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.6 | 16.2 | 81.1 | 0 | 0 | 998 | -0.21 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.8 | 13.1 | 83.1 | 0 | 0 | 998 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.3 | 16.3 | 81.9 | 0 | 0 | 998 | 0.35 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.9 | 16.9 | 80.2 | 0 | 0 | 998 | -0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2018-08-23
Weather: | Overcast
Wind conditions: | Light Wind
Air Temperature: | 19 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ (YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 19 | 80.8 | 0 | 0 | 997 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.4 | 17.4 | 80.2 | 0 | 0 | 998 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.8 | 18.1 | 81.1 | 0 | 0 | 998 | 0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 998 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 17.1 | 80.6 | 0 | 0 | 998 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 1 | 998 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.8 | 0.9 | 18 | 80.3 | 0 | 0 | 999 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22.2 | 9.9 | 11.5 | 56.4 | 0 | 1 | 998 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1 | 16.8 | 82.2 | 0 | 1 | 998 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.7 | 18.2 | 80.1 | 0 | 0 | 998 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.7 | 16.7 | 79.6 | 0 | 0 | 997 | 0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 3.2 | 17.1 | 79.7 | 0 | 0 | 998 | -0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 19.2 | 80.7 | 0 | 0 | 997 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 18.7 | 80.8 | 0 | 0 | 997 | 0 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.3 | 17.9 | 80.8 | 0 | 0 | 997 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 19.2 | 80.8 | 0 | 0 | 997 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 9.2 | 2.1 | 88.7 | 0 | 0 | 997 | 0.29 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.1 | 13 | 85.8 | 0 | 0 | 997 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Blocked | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 1.6 | 17.3 | 81 | 0 | 0 | 997 | 0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 5.9 | 12.8 | 81.2 | 0 | 0 | 996 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 19 | 81 | 0 | 0 | 997 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1 | 18.3 | 80.7 | 0 | 0 | 997 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2018-08-08 22:43 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-08-01
Date of last factory calibration | 2018-05-03
Next service due | 2018-11-03
Date of last Gas Check | 2018-05-03
Security code | [DFAB9996]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-08-08 08:32 | 53.6 | 38 | 0.4 | 8 | 992 | 195.89 | 0 | 0 | LOW
BHGV0035 | 2018-08-08 08:35 | 56.1 | 39.5 | 0.4 | 4 | 992 | -2.17 | 0 | 0 | LOW
BHGV0035 | 2018-08-08 08:35 | 55.9 | 39.4 | 0.4 | 4.3 | 992 | -4.14 | 0 | 0 | LOW
BHGV0036 | 2018-08-08 08:36 | 68.2 | 37 | 0.1 | 0 | 992 | -0.37 | 0 | 0 | LOW
BHGV0036 | 2018-08-08 08:37 | 68.3 | 36.7 | 0.1 | 0 | 992 | -1.44 | 0 | 0 | LOW
BHGV0037 | 2018-08-08 08:42 | 42.1 | 30.6 | 2 | 25.3 | 992 | 0.08 | 0 | 0 | LOW
BHM010MB | 2018-08-08 08:44 | 61 | 42.5 | 0.3 | 0 | 992 | -6.95 | 0 | 0 | LOW
BHGV0018 | 2018-08-08 08:47 | 59.8 | 44.1 | 0.1 | 0 | 992 | -7.1 | 0 | 0 | LOW
BHLC004B | 2018-08-08 08:50 | 59 | 43.8 | 0.2 | 0 | 992 | -0.03 | 0 | 0 | LOW
BHLC004B | 2018-08-08 08:51 | 59.1 | 43.5 | 0.2 | 0 | 992 | -0.81 | 0 | 0 | LOW
BHR0004B | 2018-08-08 08:54 | 66.4 | 38.6 | 0 | 0 | 992 | -5.66 | 0 | 0 | LOW
BHGV0015 | 2018-08-08 08:55 | 60.5 | 40.9 | 0.3 | 0 | 992 | -6.8 | 0 | 0 | LOW
BHGV0014 | 2018-08-08 08:56 | 60 | 44.1 | 0 | 0 | 992 | -6.94 | 0 | 0 | LOW
BHGV0013 | 2018-08-08 08:57 | 1.7 | 14.8 | 12.3 | 71.2 | 992 | -0.05 | 0 | 0 | LOW
BHGV0016 | 2018-08-08 08:59 | 21.1 | 13.5 | 11.6 | 53.8 | 992 | 0.02 | 0 | 0 | LOW
BHM010MA | 2018-08-08 09:00 | 59.3 | 41.2 | 0.7 | 0 | 992 | -6.78 | 1 | 0 | LOW
BHL000C4 | 2018-08-08 09:03 | 25.8 | 25.9 | 5 | 43.3 | 991 | -0.22 | 30 | 0 | LOW
BHL000C4 | 2018-08-08 09:03 | 26 | 24.7 | 5.3 | 44 | 991 | 0.01 | 36 | 0 | LOW
BHPRL0C4 | 2018-08-08 09:04 | 26.4 | 24.8 | 4.7 | 44.1 | 991 | -0.05 | 19 | 0 | LOW
BHPRG017 | 2018-08-08 09:08 | 27.1 | 25 | 4.9 | 43 | 991 | 0.02 | 0 | 0 | LOW
BHGV0017 | 2018-08-08 09:09 | 66.2 | 36.6 | 0.3 | 0 | 991 | -0.13 | 0 | 0 | LOW
BHGV0038 | 2018-08-08 09:10 | 61.5 | 36.7 | 0.5 | 1.3 | 991 | -1.45 | 0 | 0 | LOW
BHGV0038 | 2018-08-08 09:11 | 56.6 | 36.9 | 0.5 | 6 | 991 | -2.04 | 0 | 0 | LOW
BHGV0012 | 2018-08-08 09:13 | 60.4 | 43 | 0.1 | 0 | 991 | -5.16 | 0 | 0 | LOW
BHR00003 | 2018-08-08 09:15 | 57.1 | 33.3 | 1.8 | 7.8 | 990 | -0.22 | 0 | 0 | LOW
BHR00003 | 2018-08-08 09:16 | 57.2 | 33 | 1.8 | 8 | 990 | -4.53 | 0 | 0 | LOW
BHR00003 | 2018-08-08 09:16 | 57.2 | 32.9 | 1.8 | 8.1 | 990 | -4.41 | 0 | 0 | LOW
BHPRR003 | 2018-08-08 09:16 | 56.7 | 32.6 | 1.8 | 8.9 | 991 | -0.16 | 0 | 0 | LOW
BHGV0046 | 2018-08-08 09:19 | 32.4 | 39.5 | 1.6 | 26.5 | 990 | 1.13 | 0 | 0 | LOW
BHPRG046 | 2018-08-08 09:19 | 16.4 | 32.1 | 8.5 | 43 | 990 | 0.05 | 0 | 0 | LOW
BHR0002B | 2018-08-08 09:25 | 65.7 | 37.9 | 0.1 | 0 | 990 | 1.77 | 0 | 0 | LOW
BHPRR02B | 2018-08-08 09:25 | 65.1 | 38.6 | 0.6 | 0 | 990 | -0.21 | 0 | 0 | LOW
BHLC002B | 2018-08-08 09:29 | 38.8 | 29.3 | 4.6 | 27.3 | 990 | 0.33 | 0 | 0 | LOW
BHGV0041 | 2018-08-08 09:33 | 62 | 40.9 | 0.1 | 0 | 991 | -0.5 | 0 | 0 | LOW
BHGV0041 | 2018-08-08 09:34 | 61.6 | 41.1 | 0.1 | 0 | 991 | -1.52 | 0 | 0 | LOW
BHPRG041 | 2018-08-08 09:34 | 61.4 | 41.2 | 0 | 0 | 991 | -1.41 | 0 | 0 | LOW
BHGV0040 | 2018-08-08 09:36 | 49.3 | 36.1 | 1 | 13.6 | 991 | -6.3 | 0 | 0 | LOW
BHGV0011 | 2018-08-08 09:39 | 57.3 | 33.8 | 0.7 | 8.2 | 992 | -7.47 | 0 | 0 | LOW
BHLC001B | 2018-08-08 09:42 | 0.1 | 3.3 | 16.4 | 80.2 | 992 | -2.27 | 0 | 0 | LOW
BHGV0009 | 2018-08-08 09:42 | 62.4 | 30.9 | 0.9 | 5.8 | 992 | -6.13 | 0 | 0 | LOW
BHGV0009 | 2018-08-08 09:43 | 59.2 | 32.6 | 0.6 | 7.6 | 992 | -6.69 | 0 | 0 | LOW
BHLC0003 | 2018-08-08 09:46 | 55 | 33 | 2 | 10 | 992 | -0.09 | 0 | 0 | LOW
BHLC0003 | 2018-08-08 09:46 | 54.7 | 32.7 | 2 | 10.6 | 992 | -1.18 | 0 | 0 | LOW
BHPRL003 | 2018-08-08 09:47 | 54.8 | 32.7 | 2.1 | 10.4 | 991 | -0.13 | 0 | 0 | LOW
BHGV0301 | 2018-08-08 09:48 | 64.2 | 40.1 | 0 | 0 | 991 | -0.83 | 0 | 0 | LOW
BHGV0301 | 2018-08-08 09:49 | 62.5 | 40.9 | 0.3 | 0 | 991 | -2.13 | 0 | 0 | LOW
BHGV0045 | 2018-08-08 09:55 | 49.5 | 35.9 | 0.4 | 14.2 | 990 | -5.27 | 0 | 0 | LOW
BHGV0045 | 2018-08-08 09:56 | 49.6 | 35.9 | 0.5 | 14 | 990 | -5.63 | 0 | 0 | LOW
BHPRG045 | 2018-08-08 09:56 | 49.6 | 35.8 | 0.6 | 14 | 990 | -0.18 | 0 | 0 | LOW
BHR0001B | 2018-08-08 10:00 | 52.5 | 34.9 | 0.6 | 12 | 990 | -2.63 | 0 | 0 | LOW
BHR0001B | 2018-08-08 10:01 | 52 | 34.8 | 0.7 | 12.5 | 990 | -5.04 | 0 | 0 | LOW
BHR00001 | 2018-08-08 10:03 | 46.7 | 31.4 | 1.1 | 20.8 | 990 | -5.67 | 0 | 0 | LOW
BHGV0026 | 2018-08-08 10:06 | 60.9 | 38 | 0.5 | 0.6 | 990 | -4.47 | 0 | 0 | LOW
BHGW0034 | 2018-08-08 10:11 | 37.7 | 26.4 | 4.2 | 31.7 | 990 | 0 | 0 | 0 | LOW
BHGV0049 | 2018-08-08 10:12 | 59.2 | 36.5 | 0.7 | 3.6 | 990 | -0.78 | 0 | 0 | LOW
BHGV0049 | 2018-08-08 10:13 | 57.8 | 36.9 | 0.5 | 4.8 | 990 | -2.46 | 0 | 0 | LOW
BHPRG049 | 2018-08-08 10:13 | 57.2 | 38 | 0.8 | 4 | 990 | -0.38 | 0 | 0 | LOW
BHR0006B | 2018-08-08 10:14 | 59.8 | 42.8 | 0 | 0 | 989 | -1.57 | 0 | 0 | LOW
BHR0006B | 2018-08-08 10:14 | 59.2 | 43.4 | 0 | 0 | 989 | -2.05 | 0 | 0 | LOW
BHPRR06B | 2018-08-08 10:15 | 58.9 | 43.7 | 0.2 | 0 | 989 | -0.13 | 0 | 0 | LOW
BHPRL06B | 2018-08-08 10:16 | 59.2 | 44.1 | 0.3 | 0 | 989 | -0.13 | 0 | 0 | LOW
BHLC006B | 2018-08-08 10:17 | 59.4 | 43.6 | 0 | 0 | 989 | -2.16 | 0 | 0 | LOW
BHLC006B | 2018-08-08 10:17 | 58.1 | 44.1 | 0 | 0 | 989 | -2.47 | 0 | 0 | LOW
BHLC0006 | 2018-08-08 10:18 | 0.9 | 11.8 | 13.7 | 73.6 | 989 | -0.13 | 0 | 0 | LOW
BHLC0005 | 2018-08-08 10:19 | 2.2 | 6.1 | 15.1 | 76.6 | 989 | 0.02 | 0 | 0 | LOW
BHG01MDA | 2018-08-08 10:24 | 53.6 | 37.9 | 0.3 | 8.2 | 990 | 194.41 | 0 | 0 | LOW

## September 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-09-01
Weather: | Overcast
Wind conditions: | Light Wind
Air Temperature: | 12 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1021 | -0.31 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.6 | 15.6 | 81.8 | 0 | 0 | 1019 | -0.05 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.6 | 18.5 | 80.9 | 0 | 0 | 1019 | -0.26 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.1 | 16.9 | 82 | 0 | 0 | 1019 | -0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.2 | 15.2 | 83.2 | 0 | 0 | 1020 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 1 | 1020 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.6 | 1.6 | 15.9 | 80.9 | 0 | 0 | 1021 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22 | 9.9 | 11.5 | 56.4 | 0 | 1 | 1020 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1 | 16.8 | 82.2 | 0 | 1 | 1020 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 17.4 | 81.3 | 0 | 0 | 1019 | -0.37 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.3 | 15.3 | 81.4 | 0 | 0 | 1020 | -0.25 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.4 | 15.7 | 81.9 | 0 | 0 | 1020 | -0.17 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.7 | 16.5 | 81.8 | 0 | 0 | 1020 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.9 | 18.4 | 80.7 | 0 | 0 | 1020 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 1020 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.5 | 17.8 | 81.7 | 0 | 0 | 1020 | -0.15 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 3.6 | 8.6 | 87.8 | 0 | 0 | 1019 | -0.17 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.1 | 17.7 | 81.2 | 0 | 0 | 1020 | -0.08 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 3 | 13.9 | 83.1 | 0 | 0 | 1020 | -0.21 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 1.6 | 17.3 | 81 | 0 | 0 | 1020 | 0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.5 | 13.1 | 83.4 | 0 | 0 | 1020 | -0.13 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.4 | 15.8 | 82.2 | 0 | 0 | 1020 | -0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 3.2 | 16.4 | 80.4 | 0 | 0 | 1020 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-09-05
Weather: | Overcast
Wind conditions: | Light Wind
Air Temperature: | 12 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 19.1 | 80.4 | 0 | 0 | 1007 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.9 | 17.8 | 80.2 | 0 | 0 | 1007 | -0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.1 | 0 | 19.3 | 80.6 | 0 | 0 | 1008 | 0.23 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.1 | 0.6 | 17 | 82.3 | 0 | 0 | 1008 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 1.4 | 18.2 | 80.3 | 0 | 0 | 1008 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 1009 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.6 | 3.2 | 15.4 | 78.7 | 0 | 0 | 1009 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22 | 9.5 | 11.5 | 56 | 0 | 0 | 1009 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 16.8 | 82 | 0 | 0 | 1009 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.3 | 18.7 | 79.9 | 0 | 0 | 1007 | -0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 3.3 | 17.3 | 79.3 | 0 | 0 | 1007 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 2.8 | 17.4 | 79.7 | 0 | 0 | 1007 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 19.5 | 80.3 | 0 | 0 | 1007 | -0.71 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.6 | 18.9 | 80.4 | 0 | 0 | 1007 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0 | 19.5 | 80.4 | 0 | 0 | 1007 | -0.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 19.5 | 80.3 | 0 | 0 | 1006 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 10.3 | 0.3 | 89.3 | 0 | 0 | 1006 | -0.69 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.8 | 1.1 | 9.9 | 88.2 | 0 | 0 | 1006 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0.1 | 0.9 | 18.3 | 80.7 | 0 | 0 | 1006 | 0.57 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 7.8 | 9.7 | 82.4 | 0 | 0 | 1006 | -0.87 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4 | 16.4 | 79.5 | 0 | 0 | 1006 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.3 | 19 | 80.6 | 0 | 0 | 1006 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.9 | 18.6 | 80.4 | 0 | 0 | 1006 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-09-14
Weather: | Dry
Wind conditions: | Light Wind
Air Temperature: | 9 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.6 | 21 | 78.2 | 0 | 0 | 1000 | -0.15 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.2 | 19 | 79.6 | 0 | 0 | 1000 | -0.19 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 3.7 | 15.3 | 80.8 | 0 | 0 | 1002 | -0.16 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.2 | 1.4 | 12.3 | 82.5 | 0 | 0 | 1002 | 0.29 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 1.3 | 19.5 | 78.3 | 0 | 0 | 1002 | -0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 1001 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.3 | 2.8 | 17.4 | 76.5 | 0 | 0 | 1001 | -0.13 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 22 | 9.5 | 11.5 | 56 | 0 | 0 | 1001 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 16.8 | 82 | 0 | 0 | 1001 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 1.6 | 20.3 | 77.9 | 0 | 0 | 1001 | -0.19 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.2 | 2.1 | 19.1 | 78.6 | 0 | 0 | 1001 | -0.19 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 2.4 | 18.8 | 78.6 | 0 | 0 | 1001 | -0.19 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0.8 | 21.1 | 77.9 | 0 | 0 | 1001 | 0.12 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.2 | 0.9 | 20.2 | 78.7 | 0 | 0 | 1001 | -0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 1.2 | 20.2 | 78.4 | 0 | 0 | 1001 | -0.2 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 0.9 | 21 | 77.9 | 0 | 0 | 1001 | -0.16 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 1.1 | 20.4 | 78.3 | 0 | 0 | 1001 | -0.19 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 1.4 | 20.4 | 77.9 | 0 | 0 | 1000 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0.1 | 9.3 | 10.9 | 79.7 | 0 | 0 | 1000 | 0.69 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Blocked | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.2 | 4.6 | 14.2 | 81 | 0 | 0 | 1000 | -0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.2 | 1.3 | 20.5 | 78 | 0 | 0 | 1000 | -0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.2 | 1.1 | 20.1 | 78.6 | 0 | 0 | 1000 | -0.18 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-09-19
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.6 | 20.5 | 78.7 | 0 | 0 | 984 | -0.07 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.5 | 18.4 | 79.9 | 0 | 0 | 985 | -0.24 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 3.1 | 15.3 | 81.4 | 0 | 0 | 986 | 0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.2 | 0.9 | 12.1 | 86.8 | 0 | 0 | 986 | -0.3 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 1.3 | 18.7 | 79.1 | 0 | 0 | 986 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 986 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.7 | 1.7 | 19.8 | 77.8 | 0 | 0 | 987 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 21.6 | 9.2 | 11.5 | 57.7 | 0 | 0 | 986 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 16.4 | 82.4 | 0 | 0 | 986 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 1.8 | 20.6 | 77.4 | 0 | 0 | 985 | 0.64 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.2 | 2.1 | 19 | 78.7 | 0 | 0 | 985 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 1.9 | 18.6 | 79.3 | 0 | 0 | 985 | -0.12 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0.8 | 20.9 | 78.1 | 0 | 0 | 985 | 0.49 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.2 | 0.8 | 19.6 | 79.4 | 0 | 0 | 985 | 0.42 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 2.7 | 13.3 | 83.8 | 0 | 0 | 985 | -0.26 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 1.1 | 20.9 | 77.8 | 0 | 0 | 985 | -0.15 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 1.3 | 16.4 | 82.1 | 0 | 0 | 984 | 1.72 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 1.2 | 13.8 | 84.8 | 0 | 0 | 984 | -0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0.2 | 2.3 | 19.9 | 77.6 | 0 | 0 | 983 | 0.05 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Blocled | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.2 | 2.9 | 15.4 | 81.5 | 0 | 0 | 984 | -0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.2 | 1.3 | 19.9 | 78.4 | 0 | 0 | 984 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.2 | 1 | 19.9 | 78.9 | 0 | 0 | 984 | -0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-09-25
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1022 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.5 | 16.1 | 81.4 | 0 | 0 | 1022 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.8 | 8 | 87.2 | 0 | 0 | 1024 | 0.05 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1 | 16.2 | 82.8 | 0 | 0 | 1024 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.7 | 17.3 | 82 | 0 | 0 | 1024 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 1024 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.7 | 1.8 | 15.8 | 81.7 | 0 | 0 | 1023 | 0 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.9 | 7.4 | 13.9 | 66.8 | 0 | 0 | 1022 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 16.4 | 82.4 | 0 | 0 | 1024 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.4 | 17.4 | 82.2 | 0 | 0 | 1023 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.3 | 15.6 | 81.1 | 0 | 0 | 1022 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 17.1 | 82.1 | 0 | 0 | 1022 | 0 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1022 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 1022 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.9 | 14 | 83.1 | 0 | 0 | 1022 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1021 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.2 | 10.2 | 85.6 | 0 | 0 | 1022 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 0.7 | 13.2 | 85.8 | 0 | 0 | 1023 | 0.11 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 6.9 | 11 | 82.1 | 0 | 0 | 1023 | 0.33 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Blocked | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 15.2 | 80.2 | 0 | 0 | 1022 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 1022 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.1 | 16.5 | 82.4 | 0 | 0 | 1022 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2018-09-05 11:02 | Software Version | 1.9.11
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2018-08-13
Date of last factory calibration | 2018-05-03
Next service due | 2018-11-03
Date of last Gas Check | 2018-05-03
Security code | [942EC926]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | SITECHOSEN 1 | SITECHOSEN 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-09-05 08:55 | 46.1 | 35 | 0.8 | 18.1 | 1009 | 205.06 | 0 | 0 | LOW | sunny | light wind
BHGV0035 | 2018-09-05 08:58 | 40.5 | 34.8 | 0.5 | 24.2 | 1008 | -2.43 | 0 | 0 | LOW | sunny | light wind
BHGV0035 | 2018-09-05 09:00 | 40.4 | 34.6 | 0.9 | 24.1 | 1008 | -0.86 | 0 | 0 | LOW | sunny | light wind
BHGV0036 | 2018-09-05 09:01 | 28.1 | 29 | 0.7 | 42.2 | 1008 | -2.33 | 0 | 0 | LOW | sunny | light wind
BHGV0036 | 2018-09-05 09:01 | 28.2 | 28.2 | 0.6 | 43 | 1008 | 0.08 | 0 | 0 | LOW | sunny | light wind
BHGV0037 | 2018-09-05 09:04 | 36.6 | 30.3 | 0.6 | 32.5 | 1009 | -1.03 | 0 | 0 | LOW | sunny | light wind
BHM010MB | 2018-09-05 09:05 | 61.6 | 42.4 | 0.2 | 0 | 1009 | -7.65 | 0 | 0 | LOW | sunny | light wind
BHGV0018 | 2018-09-05 09:09 | 60.1 | 43.3 | 0 | 0 | 1008 | -7.23 | 3 | 0 | LOW | sunny | light wind
BHLC004B | 2018-09-05 09:13 | 36.2 | 28.6 | 5 | 30.2 | 1008 | 0.02 | 1 | 0 | LOW | sunny | light wind
BHR0004B | 2018-09-05 09:14 | 65.6 | 36.7 | 0.4 | 0 | 1008 | -7.64 | 0 | 0 | LOW | sunny | light wind
BHGV0015 | 2018-09-05 09:16 | 59.8 | 41.7 | 0.2 | 0 | 1008 | -8.41 | 2 | 0 | LOW | sunny | light wind
BHGV0014 | 2018-09-05 09:17 | 58.7 | 40.5 | 0.6 | 0.2 | 1008 | -7.58 | 2 | 0 | LOW | sunny | light wind
BHGV0013 | 2018-09-05 09:19 | 2 | 3 | 18.1 | 76.9 | 1008 | 0 | 0 | 0 | LOW | sunny | light wind
BHGV0016 | 2018-09-05 09:21 | 29.8 | 22.4 | 8.9 | 38.9 | 1008 | 0.06 | 2 | 0 | LOW | sunny | light wind
BHL000C4 | 2018-09-05 09:23 | 7 | 9.8 | 13.2 | 70 | 1008 | -0.43 | 11 | 0 | LOW | sunny | light wind
BHPRL0C4 | 2018-09-05 09:23 | 7 | 9.6 | 13.1 | 70.3 | 1008 | 0.04 | 12 | 0 | LOW | sunny | light wind
BHPRG017 | 2018-09-05 09:25 | 67.8 | 33.7 | 0.6 | 0 | 1007 | 0 | 0 | 0 | LOW | sunny | light wind
BHGV0017 | 2018-09-05 09:26 | 66.8 | 33.9 | 0.8 | 0 | 1007 | -7.51 | 0 | 0 | LOW | sunny | light wind
BHGV0038 | 2018-09-05 09:28 | 43.6 | 33.3 | 0.9 | 22.2 | 1008 | -2.87 | 0 | 0 | LOW | sunny | light wind
BHM010MA | 2018-09-05 09:32 | 59 | 42 | 0.1 | 0 | 1008 | -7.82 | 2 | 0 | LOW | sunny | light wind
BHLC0003 | 2018-09-05 09:35 | 7 | 6.5 | 16.1 | 70.4 | 1007 | -0.85 | 0 | 0 | LOW | sunny | light wind
BHLC0003 | 2018-09-05 09:35 | 7.3 | 6.2 | 15.9 | 70.6 | 1007 | 0.09 | 0 | 0 | LOW | sunny | light wind
BHGV0301 | 2018-09-05 09:36 | 65.2 | 38.4 | 0.2 | 0 | 1007 | -0.64 | 3 | 0 | LOW | sunny | light wind
BHGV0301 | 2018-09-05 09:38 | 63 | 38.8 | 1.7 | 0 | 1007 | -6.13 | 1 | 0 | LOW | sunny | light wind
BHGV0039 | 2018-09-05 09:41 | 44.9 | 34.6 | 1 | 19.5 | 1007 | -8.73 | 0 | 0 | LOW | sunny | light wind
BHGV0039 | 2018-09-05 09:42 | 44.2 | 34.1 | 1.2 | 20.5 | 1007 | -3.62 | 0 | 0 | LOW | sunny | light wind
BHGV0040 | 2018-09-05 09:48 | 46.3 | 35.4 | 0.5 | 17.8 | 1008 | -7.96 | 0 | 0 | LOW | sunny | light wind
BHGV0040 | 2018-09-05 09:48 | 47 | 35.1 | 0.6 | 17.3 | 1008 | -6.73 | 0 | 0 | LOW | sunny | light wind
BHLC001B | 2018-09-05 09:51 | 0.5 | 2.7 | 16.7 | 80.1 | 1008 | -2.85 | 0 | 0 | LOW | sunny | light wind
BHGV0009 | 2018-09-05 09:53 | 57.9 | 36.2 | 0.4 | 5.5 | 1008 | -8.06 | 2 | 0 | LOW | sunny | light wind
BHGV0012 | 2018-09-05 09:58 | 59.5 | 42.1 | 0.1 | 0 | 1006 | -5.95 | 2 | 0 | LOW | sunny | light wind
BHR00003 | 2018-09-05 10:00 | 22.7 | 15.4 | 11.4 | 50.5 | 1006 | -5.81 | 0 | 0 | LOW | sunny | light wind
BHR00003 | 2018-09-05 10:00 | 22.7 | 14.7 | 11.5 | 51.1 | 1006 | 0.11 | 0 | 0 | LOW | sunny | light wind
BHPRR003 | 2018-09-05 10:01 | 23 | 14.8 | 10.1 | 52.1 | 1006 | 0.06 | 0 | 0 | LOW | sunny | light wind
BHPRG046 | 2018-09-05 10:02 | 19.9 | 13.7 | 9.8 | 56.6 | 1006 | -2.26 | 0 | 0 | LOW | sunny | light wind
BHGV0046 | 2018-09-05 10:04 | 60.1 | 42.9 | 0 | 0 | 1006 | -4.1 | 3 | 0 | LOW | sunny | light wind
BHGV0046 | 2018-09-05 10:05 | 60 | 43.3 | 0.3 | 0 | 1006 | -2.57 | 2 | 0 | LOW | sunny | light wind
BHGV0041 | 2018-09-05 10:07 | 63 | 40.5 | 0.1 | 0 | 1006 | -0.96 | 4 | 0 | LOW | sunny | light wind
BHGV0041 | 2018-09-05 10:07 | 63.1 | 39.9 | 0.1 | 0 | 1006 | -1.77 | 4 | 0 | LOW | sunny | light wind
BHPRG041 | 2018-09-05 10:07 | 63 | 40 | 0.1 | 0 | 1006 | -1.89 | 4 | 0 | LOW | sunny | light wind
BHPRR02B | 2018-09-05 10:10 | 62.7 | 40 | 0.4 | 0 | 1006 | 0 | 1 | 0 | LOW | sunny | light wind
BHR0002B | 2018-09-05 10:12 | 66 | 38.4 | 0 | 0 | 1006 | 1.58 | 1 | 0 | LOW | sunny | light wind
BHGV0026 | 2018-09-05 10:13 | 57.8 | 38.2 | 0.1 | 3.9 | 1006 | -5.78 | 1 | 0 | LOW | sunny | light wind
BHLC002B | 2018-09-05 10:16 | 14 | 8.6 | 14.5 | 62.9 | 1006 | -0.47 | 0 | 0 | LOW | sunny | light wind
BHGV0045 | 2018-09-05 10:18 | 40.8 | 33.1 | 0.5 | 25.6 | 1006 | -7.17 | 0 | 0 | LOW | sunny | light wind
BHGV0045 | 2018-09-05 10:19 | 40.7 | 33.1 | 1.2 | 25 | 1006 | -2.99 | 0 | 0 | LOW | sunny | light wind
BHPRG045 | 2018-09-05 10:20 | 40.7 | 33.1 | 1.6 | 24.6 | 1006 | 0 | 0 | 0 | LOW | sunny | light wind
BHR0001B | 2018-09-05 10:22 | 48 | 33.9 | 0.4 | 17.7 | 1006 | -6.2 | 0 | 0 | LOW | sunny | light wind
BHR00001 | 2018-09-05 10:26 | 66.9 | 36.1 | 0.1 | 0 | 1006 | -7.13 | 0 | 0 | LOW | sunny | light wind
BHGV0044 | 2018-09-05 10:28 | 12.7 | 21.6 | 2 | 63.7 | 1006 | -2.34 | 0 | 0 | LOW | sunny | light wind
BHPRG044 | 2018-09-05 10:29 | 14.6 | 21.6 | 1.8 | 62 | 1006 | -0.02 | 0 | 0 | LOW | sunny | light wind
BHGV0028 | 2018-09-05 10:34 | 1.7 | 2.9 | 18.1 | 77.3 | 1005 | -3.08 | 0 | 0 | LOW | sunny | light wind
BHGV000C | 2018-09-05 10:38 | 60.4 | 41.9 | 0.1 | 0 | 1005 | -4.6 | 2 | 0 | LOW | sunny | light wind
BHGV0029 | 2018-09-05 10:41 | 53.3 | 38.5 | 0 | 8.2 | 1005 | -8.13 | 1 | 0 | LOW | sunny | light wind
BHR00005 | 2018-09-05 10:42 | 30.8 | 27 | 0.2 | 42 | 1005 | -0.01 | 0 | 0 | LOW | sunny | light wind
BHLC0005 | 2018-09-05 10:46 | 21.2 | 29.4 | 3.2 | 46.2 | 1005 | -0.01 | 1 | 0 | LOW | sunny | light wind
BHLC006B | 2018-09-05 10:48 | 59.7 | 41.8 | 0.2 | 0 | 1005 | -3.55 | 0 | 0 | LOW | sunny | light wind
BHPRR06B | 2018-09-05 10:48 | 57.1 | 41.5 | 0.6 | 0.8 | 1005 | -0.12 | 1 | 0 | LOW | sunny | light wind
BHLC0006 | 2018-09-05 10:50 | 0.4 | 12 | 14.7 | 72.9 | 1005 | -0.11 | 0 | 0 | LOW | sunny | light wind
BHGV0049 | 2018-09-05 10:51 | 37.6 | 27 | 0.6 | 34.8 | 1005 | -5.56 | 0 | 0 | LOW | sunny | light wind
BHGV0049 | 2018-09-05 10:51 | 37.4 | 28.6 | 0.4 | 33.6 | 1005 | -1 | 0 | 0 | LOW | sunny | light wind
BHGV0033 | 2018-09-05 10:53 | 38.6 | 34.3 | 0.2 | 26.9 | 1005 | -3.66 | 0 | 0 | LOW | sunny | light wind
BHGV0033 | 2018-09-05 10:53 | 38.7 | 34.4 | 0.2 | 26.7 | 1005 | -0.04 | 0 | 0 | LOW | sunny | light wind
BHGW0034 | 2018-09-05 10:55 | 30.5 | 23.6 | 3.9 | 42 | 1006 | 0.08 | 1 | 0 | LOW | sunny | light wind
BHG01MDA | 2018-09-05 10:57 | 48.4 | 35.5 | 0.4 | 15.7 | 1006 | 202.3 | 0 | 0 | LOW | sunny | light wind

## October 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-10-03
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.8 | 19.9 | 79.1 | 0 | 0 | 1019 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.3 | 18.8 | 79.8 | 0 | 0 | 1020 | -0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.1 | 2.5 | 15.7 | 81.7 | 0 | 0 | 1019 | -0.16 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.1 | 12 | 86.9 | 0 | 0 | 1019 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 1.4 | 18.9 | 79.6 | 0 | 0 | 1019 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 16.6 | 82.1 | 0 | 0 | 1019 | 0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.6 | 1.5 | 19.3 | 78.6 | 0 | 0 | 1020 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.7 | 7.5 | 13.6 | 67.2 | 0 | 0 | 1020 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 16.2 | 82.5 | 0 | 0 | 1020 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 1.8 | 20.6 | 77.4 | 0 | 0 | 1020 | -0.12 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.8 | 18.5 | 79.6 | 0 | 0 | 1019 | -0.1 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 1.5 | 18.9 | 79.4 | 0 | 0 | 1019 | -0.08 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.7 | 20.2 | 79 | 0 | 0 | 1020 | -0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.6 | 19.8 | 79.5 | 0 | 0 | 1019 | -0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 2.3 | 13.7 | 83.9 | 0 | 0 | 1019 | -0.18 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.8 | 20.4 | 78.7 | 0 | 0 | 1020 | -0.13 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.5 | 16.3 | 82.2 | 0 | 0 | 1018 | -0.13 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.4 | 13.7 | 84.8 | 0 | 0 | 1019 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0.1 | 2.5 | 19.6 | 77.8 | 0 | 0 | 1019 | -0.05 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Blocled | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 2.7 | 15.1 | 82.1 | 0 | 0 | 1019 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 1.4 | 19.7 | 78.8 | 0 | 0 | 1019 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1019 | -0.16 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-10-11
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 1.4 | 19.2 | 79.3 | 0 | 0 | 984 | -0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.5 | 18.3 | 80.1 | 0 | 0 | 983 | -0.13 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 2 | 16.3 | 81.5 | 0 | 0 | 983 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.1 | 1.3 | 12 | 86.6 | 0 | 0 | 984 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 19.6 | 79 | 0 | 0 | 984 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.7 | 82.1 | 0 | 0 | 984 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.9 | 1.5 | 18.9 | 77.7 | 0 | 0 | 985 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.8 | 7.5 | 13.8 | 66.9 | 0 | 0 | 985 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.2 | 82.4 | 0 | 0 | 985 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.3 | 19.7 | 77.9 | 0 | 0 | 983 | -0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.1 | 19 | 79.9 | 0 | 0 | 984 | 0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.4 | 18.3 | 79.3 | 0 | 0 | 984 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 1.3 | 19.6 | 79 | 0 | 0 | 983 | -0.14 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 1.8 | 19.3 | 78.8 | 0 | 0 | 984 | -0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.6 | 14.4 | 84 | 0 | 0 | 983 | 0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.7 | 19.5 | 78.8 | 0 | 0 | 983 | 0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.6 | 2.6 | 15.7 | 81.1 | 0 | 0 | 984 | -0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 1.9 | 14.1 | 83.8 | 0 | 0 | 983 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 2.2 | 19.2 | 78.6 | 0 | 0 | 982 | 0.08 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Blocked | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.1 | 15.4 | 82.5 | 0 | 0 | 982 | 0.23 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 1.1 | 19.9 | 78.9 | 0 | 0 | 984 | 0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1 | 19.1 | 79.8 | 0 | 0 | 984 | -0.16 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-10-17
Weather: | Wet
Wind conditions: | calm
Air Temperature: | 10 | OC
Instrument: | GA 2000 Plus
Serial No: | GA12960
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 16.6 | 83.1 | 0 | 0 | 1003 | 0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 15 | 82.8 | 0 | 0 | 1004 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2 | 15.1 | 82.9 | 0 | 0 | 1005 | 0.08 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.3 | 11.9 | 86.3 | 0 | 0 | 1005 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 16.6 | 82.9 | 0 | 0 | 1005 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 16.6 | 82.1 | 0 | 0 | 1005 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.8 | 1.5 | 15.3 | 82.4 | 0 | 0 | 1004 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.2 | 5.4 | 14.2 | 72.2 | 0 | 0 | 1004 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16 | 82.6 | 0 | 0 | 1004 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.9 | 16 | 83.1 | 0 | 0 | 1004 | 0.13 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.4 | 14.9 | 81.7 | 0 | 0 | 1004 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.6 | 14.8 | 82.6 | 0 | 0 | 1004 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 16.8 | 83.1 | 0 | 0 | 1004 | -0.91 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 1004 | -0.42 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.5 | 16.4 | 83.1 | 0 | 0 | 1004 | 0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 16.9 | 83 | 0 | 0 | 1004 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 9.4 | 1.7 | 88.9 | 0 | 0 | 1003 | -0.56 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.3 | 19.1 | 78.6 | 0 | 0 | 1004 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.7 | 15.4 | 81.8 | 0 | 0 | 1004 | 0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 13.6 | 81.8 | 0 | 0 | 1003 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 16.7 | 83.2 | 0 | 0 | 1003 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 1003 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-10-24
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.8 | 18.7 | 80.5 | 0 | 0 | 1024 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.9 | 16.8 | 81.3 | 0 | 0 | 1025 | 0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.1 | 1.8 | 15.9 | 82.2 | 0 | 0 | 1023 | 0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.3 | 12.8 | 85.5 | 0 | 0 | 1024 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.9 | 18.1 | 81 | 0 | 0 | 1023 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.6 | 82.2 | 0 | 0 | 1024 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.4 | 1.3 | 16.3 | 81 | 0 | 0 | 1024 | 0.12 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.3 | 5.3 | 14.6 | 71.8 | 0 | 0 | 1024 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16 | 82.6 | 0 | 0 | 1024 | 0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 19.7 | 78 | 0 | 0 | 1024 | -0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.8 | 17.7 | 80.5 | 0 | 0 | 1025 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.1 | 17.5 | 80.4 | 0 | 0 | 1023 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 18.3 | 81.1 | 0 | 0 | 1023 | -0.34 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.9 | 18.7 | 80.4 | 0 | 0 | 1024 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 15.3 | 83.6 | 0 | 0 | 1024 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1 | 18.5 | 80.5 | 0 | 0 | 1023 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.9 | 8.9 | 85.2 | 0 | 0 | 1024 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.5 | 14.6 | 83.9 | 0 | 0 | 1023 | -0.1 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.3 | 16.3 | 81.4 | 0 | 0 | 1023 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.5 | 14.8 | 81.7 | 0 | 0 | 1024 | -0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.1 | 81.4 | 0 | 0 | 1023 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.1 | 18.3 | 80.6 | 0 | 0 | 1024 | 0.11 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-10-31
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.6 | 19.8 | 79.4 | 0 | 0 | 987 | -0.18 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.5 | 18.1 | 80.2 | 0 | 0 | 988 | -0.19 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 5 | 14.4 | 80.4 | 0 | 0 | 989 | -0.19 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.2 | 0.9 | 14.4 | 84.5 | 0 | 0 | 989 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 1.2 | 18.3 | 80.3 | 0 | 0 | 989 | -0.2 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 16.6 | 82.2 | 0 | 0 | 989 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3 | 2 | 15.5 | 79.5 | 0 | 0 | 988 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15 | 8.9 | 15.5 | 60.6 | 0 | 0 | 988 | -0.21 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.5 | 16 | 82.5 | 0 | 0 | 988 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.6 | 19.1 | 79.2 | 0 | 0 | 988 | -0.18 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.9 | 17.6 | 79.4 | 0 | 0 | 988 | -0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 3.3 | 17 | 79.6 | 0 | 0 | 988 | -0.22 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0.2 | 19.9 | 79.7 | 0 | 0 | 988 | -0.19 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 20 | 79.7 | 0 | 0 | 988 | -0.21 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.5 | 2.4 | 1.6 | 95.5 | 0 | 0 | 988 | -1.75 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 20.1 | 79.7 | 0 | 0 | 988 | -0.13 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 14.4 | 84.2 | 0 | 0 | 988 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 1.3 | 19.1 | 79.4 | 0 | 0 | 987 | 0.13 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.2 | 9.4 | 10.2 | 80.2 | 0 | 0 | 987 | 0.64 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.2 | 3.1 | 16.8 | 79.9 | 0 | 0 | 987 | -0.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.2 | 0.9 | 19.7 | 79.2 | 0 | 0 | 987 | -0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.2 | 1.2 | 19 | 79.6 | 0 | 0 | 987 | 0.72 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA11919 | MCERTS certified instrument
Date downloaded | 2018-10-04 20:04 | Software Version | 1.10.0
Computer & User Info | NP-CNU0422QZW-E | paul.carroll
Date of last user calibration | 2018-10-03
Date of last factory calibration | 2018-05-30
Next service due | 2018-11-30
Date of last Gas Check | 2018-05-30
Security code | [C70F7520]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | CHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-10-04 09:17 | 54.4 | 38 | 0.4 | 7.2 | 1006 | 192.47 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0035 | 2018-10-04 09:22 | 61.4 | 41.5 | 0.2 | 0 | 1005 | 2.05 | 0 | 0 | LOW | closed | vacuum increased
BHGV0035 | 2018-10-04 09:23 | 61 | 41.6 | 1 | 0 | 1005 | -3.83 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0036 | 2018-10-04 09:25 | 69.6 | 35.3 | 0.2 | 0 | 1006 | 0.84 | 0 | 0 | LOW | closed | vacuum increased
BHGV0036 | 2018-10-04 09:25 | 69.4 | 35.7 | 0.1 | 0 | 1006 | -2.51 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0037 | 2018-10-04 09:27 | 66.9 | 35.9 | 0.5 | 0 | 1006 | 0.43 | 0 | 0 | LOW | closed | vacuum increased
BHGV0037 | 2018-10-04 09:27 | 65.4 | 36.1 | 0.6 | 0 | 1006 | -0.78 | 0 | 0 | LOW | partially open | no vacuum change
BHM010MB | 2018-10-04 09:29 | 59 | 42.5 | 0.2 | 0 | 1006 | -5.59 | 0 | 0 | LOW | fully open | no vacuum change
BHM010MB | 2018-10-04 09:29 | 59 | 42.5 | 0.4 | 0 | 1006 | -0.24 | 0 | 0 | LOW
BHM010MB | 2018-10-04 09:33 | 60.2 | 43.9 | 0 | 0 | 1006 | -5.57 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0018 | 2018-10-04 09:33 | 59.9 | 43.9 | 0 | 0 | 1005 | -25.44 | 0 | 0 | LOW
BHLC004B | 2018-10-04 09:35 | 57.9 | 41.5 | 1 | 0 | 1006 | -0.14 | 0 | 0 | LOW | closed
BHLC004B | 2018-10-04 09:36 | 56.5 | 41.8 | 1.2 | 0.5 | 1006 | -0.34 | 0 | 0 | LOW | no vacuum change
BHR0004B | 2018-10-04 09:37 | 58.1 | 41.6 | 0.1 | 0.2 | 1005 | -5.19 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0015 | 2018-10-04 09:39 | 60.8 | 43.4 | 0 | 0 | 1005 | -5.26 | 0 | 0 | LOW | fully open
BHGV0014 | 2018-10-04 09:41 | 58 | 41.7 | 0 | 0.3 | 1006 | -5.33 | 0 | 0 | LOW | fully open
BHGV0013 | 2018-10-04 09:42 | 2 | 5.9 | 17.9 | 74.2 | 1006 | 0.21 | 0 | 0 | LOW | closed | no vacuum change
BHGV0016 | 2018-10-04 09:43 | 31.6 | 21.1 | 8.6 | 38.7 | 1006 | 0.06 | 0 | 0 | LOW | closed | no vacuum change
BHL000C4 | 2018-10-04 09:45 | 33 | 20.8 | 5.7 | 40.5 | 1006 | 0.13 | 9 | 0 | LOW | closed | no vacuum change
BHPRL0C4 | 2018-10-04 09:46 | 32.7 | 21.9 | 5.8 | 39.6 | 1005 | -77.65 | 9 | 0 | LOW
BHGV0017 | 2018-10-04 09:51 | 72.1 | 28.5 | 0.2 | 0 | 1005 | -5.91 | 0 | 0 | LOW | fully open | no vacuum change
BHPRG017 | 2018-10-04 09:51 | 71.8 | 28.5 | 0.7 | 0 | 1005 | -20.79 | 0 | 0 | LOW
BHGV0038 | 2018-10-04 09:54 | 66.3 | 38.6 | 0 | 0 | 1005 | 0.44 | 0 | 0 | LOW | closed | vacuum increased
BHGV0038 | 2018-10-04 09:54 | 66.4 | 38.7 | 0.1 | 0 | 1005 | -0.81 | 0 | 0 | LOW | partially open
BHM010MA | 2018-10-04 09:56 | 59.8 | 42.1 | 0.1 | 0 | 1005 | -5.66 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0039 | 2018-10-04 09:58 | 62.6 | 34.6 | 0.3 | 2.5 | 1006 | -0.71 | 0 | 0 | LOW | closed | vacuum increased
BHGV0039 | 2018-10-04 09:59 | 62.3 | 35.1 | 0 | 2.6 | 1006 | -1.04 | 0 | 0 | LOW | partially open | no vacuum change
BHLC0003 | 2018-10-04 10:04 | 30.5 | 17.4 | 10.1 | 42 | 1005 | -2.47 | 0 | 0 | LOW | closed | no vacuum change
BHGV0301 | 2018-10-04 10:06 | 63.8 | 38.6 | 0.1 | 0 | 1005 | -3.98 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0301 | 2018-10-04 10:07 | 62.4 | 38.8 | 0.1 | 0 | 1005 | -5.65 | 0 | 0 | LOW | partially open
BHGV0040 | 2018-10-04 10:09 | 55.4 | 37.2 | 0.1 | 7.3 | 1005 | -2.99 | 0 | 0 | LOW | partially open | no vacuum change
BHLC001B | 2018-10-04 10:16 | 0.2 | 4.1 | 19.8 | 75.9 | 1006 | -1.19 | 0 | 0 | LOW | closed
BHGV0009 | 2018-10-04 10:18 | 58.3 | 39.7 | 0.1 | 1.9 | 1006 | -5.68 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0041 | 2018-10-04 10:27 | 63.3 | 40.7 | 0.1 | 0 | 1004 | -0.04 | 0 | 0 | LOW | closed | vacuum increased
BHGV0041 | 2018-10-04 10:27 | 62.7 | 41.2 | 0.6 | 0 | 1004 | -1.64 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0046 | 2018-10-04 10:29 | 60.9 | 43.6 | 0 | 0 | 1004 | -1.86 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0046 | 2018-10-04 10:30 | 59.9 | 43.9 | 0.3 | 0 | 1004 | -3.05 | 0 | 0 | LOW | partially open | no vacuum change
BHR0002B | 2018-10-04 10:33 | 67.1 | 37.8 | 0.1 | 0 | 1004 | 2.9 | 0 | 0 | LOW | fully open | no vacuum change
BHPRR02B | 2018-10-04 10:34 | 66.2 | 38 | 0.6 | 0 | 1004 | -25.13 | 0 | 0 | LOW
BHPRG046 | 2018-10-04 10:34 | 66.3 | 38.2 | 0.4 | 0 | 1004 | -3.01 | 0 | 0 | LOW
BHPRG041 | 2018-10-04 10:35 | 66.7 | 38 | 0.2 | 0 | 1004 | 0.03 | 0 | 0 | LOW
BHLC002B | 2018-10-04 10:41 | 13 | 24.9 | 6 | 56.1 | 1004 | 0.61 | 0 | 0 | LOW | closed | no vacuum change
BHGV0045 | 2018-10-04 10:43 | 64.5 | 40.4 | 0.1 | 0 | 1004 | -0.31 | 0 | 0 | LOW | closed | vacuum increased
BHGV0045 | 2018-10-04 10:44 | 64.1 | 40.8 | 0.2 | 0 | 1004 | -1.38 | 0 | 0 | LOW | partially open
BHR0001B | 2018-10-04 10:46 | 58.7 | 34.3 | 0.6 | 6.4 | 1005 | -3.51 | 0 | 0 | LOW | partially open | vacuum increased
BHR0001B | 2018-10-04 10:46 | 58.1 | 35.2 | 0.6 | 6.1 | 1005 | -3.58 | 0 | 0 | LOW | no vacuum change
BHGV0044 | 2018-10-04 10:48 | 37.9 | 26.6 | 0.9 | 34.6 | 1005 | -0.92 | 0 | 0 | LOW | partially open
BHGV0044 | 2018-10-04 10:48 | 37.7 | 26.7 | 1.1 | 34.5 | 1005 | -0.23 | 0 | 0 | LOW | closed | no vacuum change
BHGV0028 | 2018-10-04 10:53 | 12.8 | 10.1 | 16.2 | 60.9 | 1004 | -1.24 | 0 | 0 | LOW | closed | no vacuum change
BHGV000C | 2018-10-04 10:57 | 60.8 | 42.9 | 0.1 | 0 | 1004 | -2.42 | 0 | 0 | LOW | no vacuum change
BHGV0030 | 2018-10-04 10:58 | 62.7 | 35.8 | 0.4 | 1.1 | 1004 | -3.21 | 0 | 0 | LOW | partially open | no vacuum change
BHGV000B | 2018-10-04 11:00 | 63.4 | 35.3 | 0.5 | 0.8 | 1004 | -3.36 | 0 | 0 | LOW | no vacuum change
BHLC006B | 2018-10-04 11:05 | 60.3 | 39.1 | 0.4 | 0.2 | 1004 | -2.01 | 0 | 0 | LOW | partially open | vacuum increased
BHLC006B | 2018-10-04 11:06 | 59 | 40.2 | 0.5 | 0.3 | 1004 | -4.02 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0033 | 2018-10-04 11:11 | 65.5 | 40.7 | 0.2 | 0 | 1004 | 0.72 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0049 | 2018-10-04 11:13 | 61.8 | 42.5 | 0 | 0 | 1004 | 1.84 | 0 | 0 | LOW | closed | vacuum increased
BHGV0049 | 2018-10-04 11:14 | 61.8 | 42.8 | 0.2 | 0 | 1004 | -0.57 | 0 | 0 | LOW | partially open | no vacuum change
BHGW0034 | 2018-10-04 11:22 | 63.3 | 32.6 | 1 | 3.1 | 1005 | 0.37 | 0 | 0 | LOW
BHG01MDA | 2018-10-04 11:25 | 55.2 | 38.9 | 0.2 | 5.7 | 1004 | 195.17 | 0 | 0 | LOW | fully open | no vacuum change
Model | GA2000Plus | Serial No | GA11919 | MCERTS certified instrument
Date downloaded | 2018-10-31 12:35 | Software Version | 1.10.0
Computer & User Info | NP-CNU0422QZW-E | paul.carroll
Date of last user calibration | 2018-10-30
Date of last factory calibration | 2018-05-30
Next service due | 2018-11-30
Date of last Gas Check | 2018-05-30
Security code | [0DB4332A]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | CHOSEN 1 | CHOSEN 2 | CHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2018-10-31 08:47 | 52 | 35.6 | 0.4 | 12 | 987 | 188.39 | 3 | 32 | fully open | no vacuum change
BHG010MB | 2018-10-31 09:35 | 50.2 | 35.2 | 0.3 | 14.3 | 987 | -9.66 | 1 | 0 | fully open
BHGV0035 | 2018-10-31 09:38 | 60.9 | 38.8 | 0.8 | 0 | 987 | -1 | 0 | 0 | partially open | vacuum increased
BHGV0035 | 2018-10-31 09:39 | 60.1 | 39.4 | 0.6 | 0 | 987 | -7.09 | 0 | 0 | partially open | no vacuum change
BHGV0036 | 2018-10-31 09:41 | 35.6 | 24.7 | 1.3 | 38.4 | 987 | 0.44 | 0 | 0 | partially open | vacuum decreased
BHGV0036 | 2018-10-31 09:41 | 34.7 | 25.6 | 0.4 | 39.3 | 987 | -3.54 | 0 | 0 | closed | no vacuum change
BHGV0037 | 2018-10-31 09:44 | 67.6 | 35.1 | 0.1 | 0 | 987 | -2.76 | 0 | 0 | partially open | vacuum increased
BHGV0037 | 2018-10-31 09:44 | 67.6 | 34.9 | 0 | 0 | 987 | -3.65 | 0 | 0 | partially open | no vacuum change
BHM010MB | 2018-10-31 09:46 | 58.1 | 40.6 | 0 | 1.3 | 987 | -6.8 | 1 | 0 | fully open | no vacuum change
BHGV0018 | 2018-10-31 09:48 | 60.5 | 40.6 | 0.5 | 0 | 987 | -6.72 | 2 | 0 | fully open | no vacuum change
BHLC004B | 2018-10-31 09:55 | 48.6 | 36.1 | 2.8 | 12.5 | 987 | -1.17 | 1 | 0 | partially open | no vacuum change
BHR0004B | 2018-10-31 09:59 | 56.1 | 39.4 | 0 | 4.5 | 987 | -11.14 | 0 | 0 | partially open | no vacuum change
BHGV0015 | 2018-10-31 10:02 | 59.7 | 40.5 | 0.3 | 0 | 988 | -9.26 | 1 | 0 | fully open | no vacuum change
BHGV0014 | 2018-10-31 10:03 | 56.2 | 39.2 | 0.1 | 4.5 | 987 | -8.31 | 0 | 0 | fully open | no vacuum change
BHGV0013 | 2018-10-31 10:06 | 0.2 | 3.4 | 18 | 78.4 | 988 | 0.69 | 0 | 0 | closed | no vacuum change
BHGV0016 | 2018-10-31 10:10 | 22.6 | 11.3 | 13.6 | 52.5 | 987 | -1.12 | 0 | 0 | closed | no vacuum change
BHM010MA | 2018-10-31 10:12 | 58.6 | 39.4 | 0.4 | 1.6 | 987 | -9.04 | 1 | 0 | fully open | no vacuum change
BHL000C4 | 2018-10-31 10:14 | 38.5 | 27.1 | 2.7 | 31.7 | 987 | -0.14 | 9 | 0 | closed | no vacuum change
BHPRL0C4 | 2018-10-31 10:15 | 38.3 | 27.4 | 2.8 | 31.5 | 987 | -1.6 | 6 | 0
BHGV0017 | 2018-10-31 10:19 | 73.6 | 25.1 | 0.2 | 1.1 | 987 | -7.9 | 0 | 0 | fully open | no vacuum change
BHPRG017 | 2018-10-31 10:19 | 72.6 | 25.1 | 0.4 | 1.9 | 987 | -61.63 | 0 | 0
BHGV0030 | 2018-10-31 10:22 | 60.1 | 41.3 | 0.3 | 0 | 987 | -11.72 | 1 | 0 | fully open | no vacuum change
BHGV0038 | 2018-10-31 10:28 | 55.5 | 34.2 | 1.4 | 8.9 | 987 | 1.91 | 0 | 0 | closed | vacuum increased
BHGV0038 | 2018-10-31 10:29 | 56.4 | 34.9 | 1.2 | 7.5 | 987 | -3.9 | 0 | 0 | fully open | no vacuum change
BHGV0039 | 2018-10-31 10:32 | 55.9 | 32.2 | 0.5 | 11.4 | 987 | 1.26 | 0 | 0 | closed | vacuum increased
BHGV0039 | 2018-10-31 10:33 | 56.3 | 32.6 | 0.8 | 10.3 | 987 | -7.66 | 0 | 0 | partially open | no vacuum change
BHPRG039 | 2018-10-31 10:33 | 55.5 | 32.6 | 1.1 | 10.8 | 988 | -23.59 | 0 | 0
BHG010MB | 2018-10-31 10:35 | 50.9 | 32.7 | 0.1 | 16.3 | 988 | -6.76 | 0 | 0 | fully open | no vacuum change
BHGV0040 | 2018-10-31 10:38 | 56.2 | 37.4 | 0.7 | 5.7 | 988 | -7.82 | 0 | 0 | partially open | vacuum increased
BHGV0040 | 2018-10-31 10:39 | 55.9 | 37.5 | 0.7 | 5.9 | 988 | -11.6 | 0 | 0 | partially open | no vacuum change
BHLC001B | 2018-10-31 10:41 | 0.2 | 2.2 | 19.6 | 78 | 988 | -3.44 | 0 | 0 | closed | no vacuum change
BHGV0009 | 2018-10-31 10:44 | 60.6 | 38.5 | 0 | 0.9 | 988 | -8.05 | 0 | 0 | partially open | no vacuum change
BHGV0009 | 2018-10-31 10:44 | 59.5 | 38.7 | 0.1 | 1.7 | 988 | -3.21 | 0 | 0 | partially open | no vacuum change
BHLC002B | 2018-10-31 10:57 | 1.7 | 3.1 | 18 | 77.2 | 986 | -2.37 | 0 | 0 | closed | no vacuum change
BHGV0202 | 2018-10-31 11:01 | 48.9 | 33 | 0.4 | 17.7 | 986 | -6.81 | 0 | 0 | partially open | no vacuum change
BHGV0026 | 2018-10-31 11:04 | 59.2 | 38.2 | 0 | 2.6 | 986 | -8.6 | 0 | 0 | fully open | no vacuum change
BHR0002B | 2018-10-31 11:05 | 69.4 | 33.3 | 2.8 | 0 | 986 | -2.3 | 0 | 0 | fully open | no vacuum change
BHGV0046 | 2018-10-31 11:07 | 57.8 | 39.2 | 1 | 2 | 986 | -1.72 | 0 | 0 | partially open | vacuum increased
BHGV0046 | 2018-10-31 11:07 | 57.3 | 39.6 | 0.9 | 2.2 | 986 | -6.8 | 1 | 0 | partially open | no vacuum change
BHGV000A | 2018-10-31 11:09 | 62.6 | 39.3 | 0.7 | 0 | 986 | -2.1 | 1 | 0 | fully open | no vacuum change
BHGV0041 | 2018-10-31 11:13 | 61.3 | 40.1 | 1.2 | 0 | 986 | -0.95 | 1 | 0 | closed | vacuum increased
BHGV0041 | 2018-10-31 11:14 | 60.9 | 40 | 2 | 0 | 986 | -6.55 | 0 | 0 | partially open | no vacuum change
BHGV0028 | 2018-10-31 11:20 | 0.2 | 1.3 | 19.6 | 78.9 | 986 | -2.27 | 0 | 0 | closed | no vacuum change
BHGV0029 | 2018-10-31 11:23 | 54 | 34.6 | 0.2 | 11.2 | 986 | -6.61 | 0 | 0 | fully open | no vacuum change
BHR00005 | 2018-10-31 11:25 | 24.6 | 20.5 | 0.9 | 54 | 986 | 0.05 | 0 | 0 | closed | no vacuum change
BHGV0031 | 2018-10-31 11:26 | 60.2 | 36.3 | 0.4 | 3.1 | 986 | -5.87 | 0 | 0 | partially open | no vacuum change
BHLC0005 | 2018-10-31 11:30 | 49.7 | 35.2 | 2.8 | 12.3 | 986 | -0.95 | 0 | 0 | partially open | no vacuum change
BHLC0005 | 2018-10-31 11:30 | 49.6 | 35.9 | 2.7 | 11.8 | 986 | -3.1 | 0 | 0 | partially open | no vacuum change
BHLC006B | 2018-10-31 11:32 | 55.9 | 37.9 | 0.3 | 5.9 | 986 | -1.75 | 0 | 0 | partially open | vacuum increased
BHLC006B | 2018-10-31 11:33 | 55.6 | 38.3 | 0.4 | 5.7 | 986 | -2.93 | 1 | 0 | partially open | no vacuum change
BHGV0033 | 2018-10-31 11:35 | 62.7 | 39.1 | 0.5 | 0 | 986 | -1.71 | 0 | 0 | partially open | no vacuum change
BHGV0022 | 2018-10-31 11:39 | 65.8 | 37.8 | 0.1 | 0 | 987 | 22.45 | 0 | 0 | fully open | no vacuum change
BHGV0023 | 2018-10-31 11:45 | 63.7 | 37.9 | 0.4 | 0 | 987 | -8.53 | 0 | 0 | fully open | no vacuum change
BHGV0048 | 2018-10-31 11:48 | 68.1 | 35.2 | 3.6 | 0 | 987 | -0.42 | 0 | 0 | fully open | no vacuum change
BHGV0024 | 2018-10-31 11:51 | 56.7 | 37 | 0.8 | 5.5 | 987 | -6.93 | 0 | 0 | no vacuum change
BHGW0034 | 2018-10-31 12:02 | 54.4 | 29.6 | 0.1 | 15.9 | 987 | -2.92 | 0 | 0 | partially open | no vacuum change
BHG010MA | 2018-10-31 12:04 | 52.7 | 33.3 | 0.7 | 13.3 | 987 | -9.21 | 0 | 0 | fully open | no vacuum change
BHG01MDA | 2018-10-31 12:14 | 52.1 | 34.7 | 0.6 | 12.6 | 987 | 182.58 | 0 | 0 | fully open | no vacuum change

## November 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-11-07
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.8 | 19.6 | 79.5 | 0 | 0 | 976 | -0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.1 | 18.8 | 80 | 0 | 0 | 975 | -0.18 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.3 | 14.9 | 80.8 | 0 | 0 | 976 | 0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.2 | 1.3 | 13.9 | 84.6 | 0 | 0 | 976 | 0.22 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.8 | 18.5 | 80.6 | 0 | 0 | 975 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 15.4 | 83.4 | 0 | 0 | 975 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.3 | 2.3 | 15.8 | 78.6 | 0 | 0 | 975 | 0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.5 | 8.4 | 15.8 | 59.9 | 0 | 0 | 975 | 0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.5 | 16 | 82.5 | 0 | 0 | 975 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 1.4 | 19.5 | 78.9 | 0 | 0 | 976 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.2 | 2.5 | 17.2 | 80.1 | 0 | 0 | 975 | 0.07 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 2.8 | 16.9 | 80.2 | 0 | 0 | 975 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.4 | 19.3 | 80.2 | 0 | 0 | 975 | 0.18 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 19.8 | 79.9 | 0 | 0 | 975 | 0.26 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.3 | 1.9 | 1.9 | 95.9 | 0 | 0 | 975 | 0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 19.5 | 80.1 | 0 | 0 | 976 | 0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 1.3 | 19.2 | 79.3 | 0 | 0 | 976 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.2 | 18.7 | 80 | 0 | 0 | 975 | 0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 9.4 | 10.8 | 79.7 | 0 | 0 | 975 | 0.32 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.3 | 16.3 | 80.4 | 0 | 0 | 976 | -0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.7 | 19.2 | 80 | 0 | 0 | 975 | 0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.2 | 1.1 | 18.4 | 80.3 | 0 | 0 | 975 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-11-15
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 7 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1 | 19.1 | 79.9 | 0 | 0 | 1001 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 1000 | -0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.7 | 14.4 | 80.9 | 0 | 0 | 1001 | -0.25 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.1 | 14.1 | 84.8 | 0 | 0 | 1001 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.7 | 18.9 | 80.3 | 0 | 0 | 1000 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 15.2 | 83.6 | 0 | 0 | 100 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.2 | 2.1 | 15.4 | 76.3 | 0 | 0 | 1000 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.3 | 7.9 | 15.3 | 62.5 | 0 | 0 | 1000 | -0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.1 | 82.5 | 0 | 0 | 100 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 19.3 | 79.6 | 0 | 0 | 1000 | -0.14 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.9 | 16.8 | 80.2 | 0 | 0 | 1001 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 3.6 | 16.4 | 80 | 0 | 0 | 1000 | -0.09 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.7 | 18.9 | 80.4 | 0 | 0 | 1000 | 0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 19.4 | 80.3 | 0 | 0 | 1000 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 2.4 | 2.4 | 95 | 0 | 0 | 1000 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 1000 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 1.4 | 19.1 | 79.3 | 0 | 0 | 100 | 0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1 | 18.4 | 80.6 | 0 | 0 | 1000 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocled | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 9.8 | 11.4 | 78.8 | 0 | 0 | 1000 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3 | 16.7 | 80.3 | 0 | 0 | 1000 | -0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.9 | 80.6 | 0 | 0 | 1001 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.5 | 18.1 | 80.3 | 0 | 0 | 1000 | -0.22 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-11-23
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 7 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.7 | 19.7 | 79.4 | 0 | 0 | 1000 | 0.89 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.4 | 19 | 79.4 | 0 | 0 | 1000 | 0.32 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 3.8 | 13.5 | 82.5 | 0 | 0 | 1002 | 0.38 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.2 | 0.8 | 17.8 | 81.2 | 0 | 0 | 1002 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 0.9 | 19.4 | 79.5 | 0 | 0 | 1002 | 0.72 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 15.4 | 83.3 | 0 | 0 | 1001 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.6 | 3.5 | 16 | 76.9 | 0 | 0 | 1001 | 1.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.3 | 8.9 | 15 | 60.8 | 0 | 0 | 1000 | 0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.4 | 16.2 | 81.4 | 0 | 0 | 1001 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.9 | 19.8 | 79.1 | 0 | 0 | 1000 | 0.36 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.2 | 2.5 | 18.4 | 78.9 | 0 | 0 | 1001 | 2.53 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 2.3 | 19 | 78.5 | 0 | 0 | 1001 | 1.84 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0.2 | 20.2 | 79.4 | 0 | 0 | 1000 | 0.73 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.2 | 0.3 | 20.2 | 79.3 | 0 | 0 | 1000 | 1.9 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.8 | 6 | 5.9 | 87.3 | 0 | 0 | 1000 | 2.1 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 0.1 | 20.1 | 79.6 | 0 | 0 | 1000 | 0.69 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 1.3 | 18.9 | 79.6 | 0 | 0 | 100 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 2.5 | 18.8 | 78.4 | 0 | 0 | 1000 | 0.72 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.2 | 9.3 | 10.9 | 79.8 | 0 | 0 | 1000 | 0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.2 | 4.7 | 13.5 | 81.6 | 0 | 0 | 1000 | 0.67 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.2 | 1.3 | 19.3 | 78.9 | 0 | 0 | 1000 | 1.26 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.2 | 1.1 | 19.4 | 79.3 | 0 | 0 | 1000 | -1.2 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-11-29
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.1 | 18.5 | 80.4 | 0 | 0 | 973 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 973 | -0.14 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 5 | 14.1 | 80.9 | 0 | 0 | 973 | -0.21 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.4 | 14.7 | 83.9 | 0 | 0 | 974 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.1 | 18.5 | 80.4 | 0 | 0 | 974 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 15.6 | 83.2 | 0 | 0 | 974 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.9 | 3.1 | 15.1 | 73.9 | 0 | 0 | 974 | -0.17 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.8 | 8.9 | 14.5 | 61.8 | 0 | 0 | 975 | -0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.3 | 16.3 | 82.3 | 0 | 0 | 975 | 0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.8 | 18.7 | 80.5 | 0 | 0 | 975 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.3 | 17.1 | 80.6 | 0 | 0 | 975 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 4.2 | 15.9 | 79.9 | 0 | 0 | 974 | 0.19 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 18.3 | 80.8 | 0 | 0 | 974 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19.1 | 80.4 | 0 | 0 | 974 | -0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 2.9 | 2.1 | 94.9 | 0 | 0 | 974 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 974 | -0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.2 | 18.8 | 80 | 0 | 0 | 974 | 0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.3 | 18 | 80.7 | 0 | 0 | 974 | -0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 9.2 | 11.9 | 78.9 | 0 | 0 | 973 | 0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.3 | 16.9 | 80.8 | 0 | 0 | 973 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.8 | 18.3 | 80.9 | 0 | 0 | 973 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 18.8 | 79.9 | 0 | 0 | 974 | -0.2 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA11919 | MCERTS certified instrument
Date downloaded | 2018-10-31 12:35 | Software Version | 1.10.0
Computer & User Info | NP-CNU0422QZW-E | paul.carroll
Date of last user calibration | 2018-11-29
Date of last factory calibration | 2018-05-30
Next service due | 2018-11-30
Date of last Gas Check | 2018-05-30
Security code | [0DB4332A]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2018-11-29 11:04 | 50.1 | 37 | 0.5 | 12.4 | 975 | 176.52 | 0 | 0 | LOW | fully open | no vacuum change
BHG010MB | 2018-11-29 11:11 | 49.9 | 37.1 | 0.5 | 12.5 | 978 | -10.78 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0035 | 2018-11-29 11:14 | 59.6 | 37.8 | 0.6 | 2 | 974 | -6.89 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0035 | 2018-11-29 11:15 | 59.5 | 37.6 | 0.6 | 2.3 | 975 | 8.85 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0036 | 2018-11-29 11:18 | 54.4 | 31.1 | 0.4 | 14.1 | 974 | -4.51 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0036 | 2018-11-29 11:19 | 54.2 | 30.9 | 0.4 | 14.5 | 975 | -6.52 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0037 | 2018-11-29 11:21 | 61.5 | 34.2 | 0.2 | 4.1 | 974 | -4.23 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0037 | 2018-11-29 11:22 | 61.5 | 34.1 | 0.2 | 4.2 | 974 | -5.86 | 1 | 0 | LOW | partially open | no vacuum change
BHM010MB | 2018-11-29 11:25 | 57.4 | 39.7 | 0.1 | 2.8 | 975 | -9.36 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0018 | 2018-11-29 11:27 | 59.9 | 40.1 | 0.3 | 0 | 976 | -6.82 | 0 | 0 | LOW | fully open | no vacuum change
BHLC004B | 2018-11-29 11:28 | 46.3 | 32.4 | 2.9 | 18.4 | 974 | -2.32 | 2 | 0 | LOW | partially open | no vacuum change
BHR0004B | 2018-11-29 11:29 | 54.5 | 38.8 | 0.1 | 6.6 | 975 | -9.85 | 2 | 0 | LOW | partially open | no vacuum change
BHGV0015 | 2018-11-29 11:32 | 59.1 | 40.2 | 0.4 | 0.3 | 974 | -8.83 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0014 | 2018-11-29 11:34 | 56.7 | 39.5 | 0.1 | 3.7 | 974 | -7.53 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0013 | 2018-11-29 11:37 | 0.1 | 3.4 | 17.6 | 78.9 | 974 | 0.09 | 0 | 0 | LOW | closed | no vacuum change
BHGV0016 | 2018-11-29 11:39 | 24.9 | 12.5 | 12.9 | 49.7 | 974 | -0.89 | 1 | 0 | LOW | closed | no vacuum change
BHM010MA | 2018-11-29 11:41 | 57.3 | 39.5 | 0.2 | 3 | 974 | -9.56 | 2 | 0 | LOW | fully open | no vacuum change
BHL000C4 | 2018-11-29 11:45 | 42.1 | 29.7 | 2.3 | 25.9 | 974 | -0.04 | 4 | 0 | LOW | closed | no vacuum change
BHGV0017 | 2018-11-29 11:48 | 72.9 | 26.7 | 0.1 | 0.3 | 974 | -8.32 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0030 | 2018-11-29 11:50 | 59.5 | 40.4 | 0.2 | 0 | 974 | -9.85 | 3 | 0 | LOW | fully open | no vacuum change
BHGV0038 | 2018-11-29 11:53 | 56.3 | 34.8 | 1.1 | 7.8 | 975 | -6.52 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0039 | 2018-11-29 11:56 | 52.8 | 31.1 | 0.7 | 15.4 | 974 | -0.02 | 0 | 0 | LOW | closed | vacuum increased
BHGV0039 | 2018-11-29 11:57 | 52.7 | 31.1 | 0.7 | 15.5 | 976 | -2.17 | 2 | 0 | LOW | partially open | no vacuum change
BHLC0003 | 2018-11-29 11:59 | 34.4 | 18.9 | 9.7 | 37 | 974 | -1.15 | 0 | 0 | LOW | closed | no vacuum change
BHGV0301 | 2018-11-29 12:02 | 57.9 | 35.8 | 0.2 | 6.1 | 974 | -2.96 | 1 | 0 | LOW | partially open | vacuum increased
BHGV0301 | 2018-11-29 12:03 | 57.8 | 35.7 | 0.2 | 6.3 | 975 | -4.25 | 2 | 0 | LOW | partially open | no vacuum change
BHGV0040 | 2018-11-29 12:06 | 51.2 | 35.3 | 0.9 | 12.6 | 975 | -7.75 | 0 | 0 | LOW | partially open | no vacuum change
BHLC001B | 2018-11-29 12:09 | 0.1 | 2.3 | 19.3 | 78.3 | 975 | -4.18 | 0 | 0 | LOW | closed | no vacuum change
BHGV0009 | 2018-11-29 12:11 | 59.1 | 37.9 | 0.2 | 2.8 | 974 | -7.63 | 1 | 0 | LOW | partially open | vacuum increased
BHGV0009 | 2018-11-29 12:12 | 59.2 | 38 | 0.2 | 2.6 | 975 | -8.88 | 0 | 0 | LOW | partially open | no vacuum change
BHLC002B | 2018-11-29 12:15 | 2.2 | 3.4 | 17.5 | 76.9 | 974 | -0.76 | 2 | 0 | LOW | closed | no vacuum change
BHGV0202 | 2018-11-29 12:18 | 46.9 | 32.1 | 0.6 | 20.4 | 974 | -2.34 | 0 | 0 | LOW | partially open | vacuum decreased
BHGV0202 | 2018-11-29 12:19 | 46.8 | 32.1 | 0.6 | 20.5 | 974 | -1.12 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0026 | 2018-11-29 12:24 | 58.8 | 37.8 | 0 | 3.4 | 974 | -9.24 | 2 | 0 | LOW | fully open | no vacuum change
BHR0002B | 2018-11-29 12:27 | 68.2 | 32.9 | 2.5 | 0 | 975 | -7.88 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0045 | 2018-11-29 12:30 | 48.9 | 33.5 | 0.9 | 16.7 | 974 | -5.57 | 1 | 0 | LOW | partially open | no vacuum change
BHR0001B | 2018-11-29 12:33 | 52.3 | 33.4 | 0.6 | 13.7 | 973 | -4.78 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0044 | 2018-11-29 12:37 | 43.2 | 27.7 | 0.9 | 28.2 | 974 | -0.24 | 0 | 0 | LOW | closed | no vacuum change
BHGV0046 | 2018-11-29 12:41 | 51.3 | 38.7 | 1.2 | 8.8 | 974 | -4.52 | 5 | 0 | LOW | partially open | no vacuum change
BHGV000A | 2018-11-29 12:44 | 61.5 | 39.1 | 0.8 | 0 | 974 | -8.85 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0041 | 2018-11-29 12:49 | 54.3 | 37.5 | 1.9 | 6.3 | 973 | -4.78 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0044 | 2018-11-29 12:53 | 39.8 | 27.6 | 0.8 | 31.8 | 793 | -0.25 | 0 | 0 | LOW | closed | no vacuum change
BHGV000C | 2018-11-29 12:58 | 58.9 | 40.8 | 0.2 | 0.1 | 973 | -7.66 | 2 | 0 | LOW | partially open | vacuum increased
BHGV000C | 2018-11-29 12:59 | 58.8 | 40.8 | 0.2 | 0.2 | 974 | -8.56 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0030 | 2018-11-29 13:02 | 59.9 | 35.4 | 0.2 | 4.5 | 975 | -6.12 | 2 | 0 | LOW | partially open | vacuum increased
BHGV0030 | 2018-11-29 13:03 | 59.7 | 35.3 | 0.2 | 4.8 | 974 | -7.49 | 1 | 0 | LOW | partially open | no vacuum change
BHGV000B | 2018-11-29 13:07 | 59.9 | 34.9 | 0.8 | 4.4 | 974 | -4.35 | 1 | 0 | LOW | partially open | vacuum increased
BHGV000B | 2018-11-29 13:08 | 59.6 | 34.7 | 0.9 | 4.8 | 974 | -5.27 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0028 | 2018-11-29 13:13 | 0.4 | 1.5 | 18.9 | 79.2 | 975 | -1.47 | 1 | 0 | LOW | closed | no vacuum change
BHGV0029 | 2018-11-29 13:17 | 54.6 | 34.2 | 0.3 | 10.9 | 975 | -7.99 | 0 | 0 | LOW | fully open | no vacuum change
BHR0001B | 2018-11-29 13:20 | 54.3 | 34.2 | 0.9 | 10.6 | 974 | -2.45 | 2 | 0 | LOW | partially open | no vacuum change
BHR00005 | 2018-11-29 13:24 | 25.5 | 20.8 | 0.8 | 52.9 | 974 | -0.03 | 0 | 0 | LOW | closed | no vacuum change
BHGV0031 | 2018-11-29 13:27 | 58.4 | 35.8 | 0.6 | 5.2 | 974 | -6.94 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0031 | 2018-11-29 13:28 | 58.4 | 35.8 | 0.6 | 5.2 | 974 | -6.38 | 3 | 0 | LOW | partially open | no vacuum change
BHLC0005 | 2018-11-29 13:33 | 49.1 | 35.2 | 2.2 | 13.5 | 974 | -3.36 | 0 | 0 | LOW | partially open | no vacuum change
BHLC006B | 2018-11-29 13:37 | 51.3 | 35.6 | 0.5 | 12.6 | 974 | -4.58 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0033 | 2018-11-29 13:40 | 56.1 | 38.4 | 0.7 | 4.8 | 974 | -7.32 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0049 | 2018-11-29 13:45 | 56.4 | 39.8 | 0.3 | 3.5 | 974 | -5.86 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0022 | 2018-11-29 13:48 | 58.9 | 35.8 | 0.2 | 5.1 | 974 | 16.56 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0023 | 2018-11-29 13:52 | 59.6 | 36.2 | 0.7 | 3.5 | 974 | -7.89 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0048 | 2018-11-29 13:55 | 64.5 | 34.3 | 3.8 | 0 | 974 | -4.78 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0024 | 2018-11-29 13:59 | 56.7 | 37 | 0.8 | 5.5 | 974 | -3.48 | 0 | 0 | LOW | partially open | no vacuum change
BHGW0034 | 2018-11-29 14:05 | 50.3 | 28.8 | 0.3 | 20.6 | 974 | -3.72 | 0 | 0 | LOW | partially open | no vacuum change
BHG010MA | 2018-11-29 14:11 | 52.1 | 35.7 | 0.4 | 11.8 | 974 | -9.94 | 0 | 0 | LOW | fully open | no vacuum change
BHG01MDA | 2018-11-29 14:17 | 52.3 | 35.8 | 0.3 | 11.6 | 974 | 181 | 0 | 0 | LOW | fully open | no vacuum change

## December 2018
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-12-05
Weather: | Dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 1006 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.1 | 18.5 | 80.4 | 0 | 0 | 1007 | -0.13 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.7 | 14.9 | 80.4 | 0 | 0 | 1005 | 0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1 | 14.2 | 84.8 | 0 | 0 | 1006 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.3 | 18 | 80.7 | 0 | 0 | 1006 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 15.7 | 83 | 0 | 0 | 1006 | -0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.1 | 2.6 | 15.8 | 74.5 | 0 | 0 | 1005 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.9 | 8.4 | 15.1 | 63.6 | 0 | 0 | 1006 | -0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.2 | 16.1 | 82.6 | 0 | 0 | 1006 | -0.06 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 1007 | -0.08 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.5 | 17.5 | 80 | 0 | 0 | 1006 | -0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 3.3 | 16.1 | 80.6 | 0 | 0 | 1006 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 1005 | -0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1005 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.4 | 2.5 | 95.1 | 0 | 0 | 1006 | 0.09 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.6 | 19.1 | 80.3 | 0 | 0 | 1006 | -0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.3 | 18.2 | 80.5 | 0 | 0 | 1006 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.4 | 18.4 | 80.2 | 0 | 0 | 1006 | -0.12 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 8.8 | 12.4 | 78.8 | 0 | 0 | 1006 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 16.2 | 81.8 | 0 | 0 | 1006 | -0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 18.8 | 80.5 | 0 | 0 | 1007 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1 | 18.9 | 80.1 | 0 | 0 | 1006 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-12-14
Weather: | light rain
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.9 | 19.1 | 80 | 0 | 0 | 1008 | 0.22 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.8 | 18.1 | 80.1 | 0 | 0 | 1007 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.3 | 15.6 | 80.1 | 0 | 0 | 1007 | -0.16 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.3 | 15.4 | 83.3 | 0 | 0 | 1008 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.1 | 18.7 | 80.2 | 0 | 0 | 1008 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.2 | 15.9 | 82.9 | 0 | 0 | 1008 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.8 | 3.1 | 15.1 | 74 | 0 | 0 | 1008 | -0.09 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.3 | 9.2 | 13.7 | 61.8 | 0 | 0 | 1008 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.3 | 16.5 | 82.1 | 0 | 0 | 1008 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.9 | 18.9 | 80.2 | 0 | 0 | 1008 | -0.17 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.9 | 18 | 79.1 | 0 | 0 | 1008 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 4.1 | 15.7 | 80.2 | 0 | 0 | 1008 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 1008 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 18.1 | 81.2 | 0 | 0 | 1007 | -0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 3.1 | 2.4 | 94.5 | 0 | 0 | 1008 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.7 | 18.6 | 80.7 | 0 | 0 | 1008 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.2 | 18 | 80.8 | 0 | 0 | 1008 | -0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.9 | 18.1 | 80 | 0 | 0 | 1008 | -0.16 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 6.9 | 12.8 | 80.3 | 0 | 0 | 1008 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.6 | 15.7 | 81.7 | 0 | 0 | 1008 | -0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.2 | 18.3 | 80.5 | 0 | 0 | 1007 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.3 | 18.3 | 79.4 | 0 | 0 | 1008 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2018-12-19
Weather: | light rain
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA11919
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 989 | -0.14 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 17.6 | 80.2 | 0 | 0 | 989 | -0.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.8 | 15.5 | 79.7 | 0 | 0 | 989 | -0.08 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.2 | 16.1 | 82.7 | 0 | 0 | 989 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 18.6 | 80 | 0 | 0 | 989 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1 | 15.9 | 83.1 | 0 | 0 | 989 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.9 | 3.5 | 12.4 | 75.2 | 0 | 0 | 989 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.9 | 8.5 | 14.2 | 65.4 | 0 | 0 | 989 | -0.32 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 16 | 82.9 | 0 | 0 | 989 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.8 | 18.5 | 79.7 | 0 | 0 | 989 | -0.07 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.6 | 17.8 | 78.6 | 0 | 0 | 989 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 3.8 | 15.9 | 80.3 | 0 | 0 | 989 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.4 | 18 | 80.6 | 0 | 0 | 989 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.8 | 18.5 | 80.7 | 0 | 0 | 989 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 3.9 | 2.6 | 93.3 | 0 | 0 | 989 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1 | 18.5 | 80.5 | 0 | 0 | 989 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.2 | 18 | 80.8 | 0 | 0 | 989 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.5 | 18.3 | 80.1 | 0 | 0 | 989 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 6.4 | 13.5 | 80.1 | 0 | 0 | 989 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 2.4 | 16.3 | 81.2 | 0 | 0 | 989 | -0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.4 | 17.9 | 80.7 | 0 | 0 | 989 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.8 | 18.1 | 79.1 | 0 | 0 | 988 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## January 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-01-08
Weather: | light rain
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA 2000 Plus
Serial No: | GA13202
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.8 | 81 | 0 | 0 | 1011 | 0.16 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 1012 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.1 | 18.9 | 80.9 | 0 | 0 | 1012 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.9 | 2.2 | 17.1 | 77.8 | 0 | 0 | 1011 | 0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.3 | 5.7 | 15.8 | 69.2 | 0 | 0 | 1011 | 0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.2 | 16.6 | 82.1 | 0 | 0 | 1011 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.7 | 9.6 | 89.7 | 0 | 0 | 1012 | 0.88 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.6 | 10.5 | 86.8 | 0 | 0 | 1012 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.1 | 17.1 | 81.8 | 0 | 0 | 1011 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18.8 | 81.1 | 0 | 0 | 1011 | 0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 1011 | -0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 17.6 | 81.2 | 0 | 0 | 1011 | 0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 18.7 | 81.2 | 0 | 0 | 1011 | 0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 18.1 | 80.8 | 0 | 0 | 1012 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.8 | 18 | 80.2 | 0 | 0 | 1012 | -0.12 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.7 | 17.5 | 81.7 | 0 | 0 | 1011 | 0 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 4.3 | 15.5 | 80.1 | 0 | 0 | 1010 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 18.8 | 81 | 0 | 0 | 1010 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 1011 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-01-15
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 16.5 | 83.4 | 0 | 0 | 1003 | -0.86 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.2 | 16.2 | 82.6 | 0 | 0 | 1004 | -1.27 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.1 | 4.8 | 15.3 | 78.1 | 0 | 0 | 1005 | -1.46 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.4 | 16.2 | 81.7 | 0 | 0 | 1005 | -1.4 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 16.6 | 83.1 | 0 | 0 | 1005 | -0.99 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 16.7 | 83.3 | 0 | 0 | 1005 | 0.33 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.2 | 3.5 | 9.5 | 73.8 | 0 | 0 | 1003 | -0.47 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.1 | 9.5 | 12.2 | 62.2 | 0 | 0 | 1004 | -1.45 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1 | 16.4 | 82.5 | 0 | 0 | 1004 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 9.6 | 88.9 | 0 | 0 | 1003 | -0.54 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.9 | 8.3 | 87.8 | 0 | 0 | 1003 | -0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.7 | 16.4 | 82.9 | 0 | 0 | 1003 | -0.73 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 16.7 | 83.2 | 0 | 0 | 1003 | 0.52 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16.7 | 83.1 | 0 | 0 | 1004 | -0.3 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 4.4 | 13.2 | 82.4 | 0 | 0 | 1003 | -1.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 16.7 | 83.3 | 0 | 0 | 1002 | -0.78 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.7 | 8 | 0.2 | 91.1 | 0 | 0 | 1004 | 0 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 0.7 | 14.4 | 84.8 | 0 | 0 | 1004 | 0.23 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 5.6 | 11.3 | 83 | 0 | 0 | 1004 | 5.43 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3 | 15.4 | 81.6 | 0 | 0 | 1004 | -0.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 16.5 | 83.4 | 0 | 0 | 1003 | -0.57 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 15.8 | 82.9 | 0 | 0 | 1003 | -0.29 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-01-23
Weather: | dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 16.9 | 82.9 | 0 | 0 | 993 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.8 | 16.7 | 82.5 | 0 | 0 | 993 | 0.05 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.2 | 5 | 14.8 | 80 | 0 | 0 | 993 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 992 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 16.1 | 83.3 | 0 | 0 | 992 | 0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 16.3 | 83.6 | 0 | 0 | 992 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 11.2 | 3.4 | 10.1 | 75.3 | 0 | 0 | 993 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 19.9 | 10.1 | 9.8 | 60.2 | 0 | 0 | 993 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.6 | 82.2 | 0 | 0 | 993 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.8 | 9.9 | 88.3 | 0 | 0 | 993 | -0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.1 | 8.9 | 88 | 0 | 0 | 993 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 16 | 82.6 | 0 | 0 | 993 | -0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 16.4 | 83.4 | 0 | 0 | 992 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16.9 | 82.9 | 0 | 0 | 993 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 5.1 | 12.9 | 82 | 0 | 0 | 993 | 0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.6 | 82.4 | 0 | 0 | 992 | -0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.5 | 7.5 | 0.3 | 91.7 | 0 | 0 | 993 | 0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 0.5 | 14.1 | 85.2 | 0 | 0 | 993 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 5.1 | 11.8 | 83.1 | 0 | 0 | 992 | 0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 15.6 | 81.9 | 0 | 0 | 993 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 16.1 | 83.6 | 0 | 0 | 993 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 16.1 | 82.2 | 0 | 0 | 992 | -0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-01-30
Weather: | dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 16.2 | 83.5 | 0 | 0 | 984 | -0.23 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 16 | 83.1 | 0 | 0 | 985 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4.5 | 15.5 | 80 | 0 | 0 | 984 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.1 | 16.3 | 82.6 | 0 | 0 | 984 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 16.9 | 82.8 | 0 | 0 | 982 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 15.8 | 84 | 0 | 0 | 984 | 0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 10.3 | 2.9 | 10.5 | 76.3 | 0 | 0 | 984 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 18.1 | 9.6 | 10.3 | 62 | 0 | 0 | 983 | -0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.2 | 16.5 | 82.2 | 0 | 0 | 984 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 9.4 | 89.5 | 0 | 0 | 983 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.6 | 9.5 | 87.9 | 0 | 0 | 983 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.6 | 82.1 | 0 | 0 | 984 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 16 | 83.4 | 0 | 0 | 983 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 15.9 | 83.4 | 0 | 0 | 982 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 4.6 | 13.3 | 82.1 | 0 | 0 | 983 | 0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.2 | 82.7 | 0 | 0 | 982 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.3 | 7.1 | 0.6 | 92 | 0 | 0 | 984 | 0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 0.4 | 14.8 | 84.7 | 0 | 0 | 985 | 0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Blocked | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 4.4 | 12.7 | 82.9 | 0 | 0 | 984 | -0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 15.8 | 82.2 | 0 | 0 | 985 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 16.5 | 83.3 | 0 | 0 | 984 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 16.7 | 81.7 | 0 | 0 | 984 | 0.12 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2019-01-30 13:42 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2019-01-25
Date of last factory calibration | 2018-11-15
Next service due | 2019-05-15
Date of last Gas Check | 2018-11-15
Security code | [9B77D628]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | CHOSEN 1 | SITECHOSEN 1 | SITECHOSEN 2
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-01-29 10:35 | 51.2 | 35.5 | 0.5 | 12.8 | 981 | 162.33 | 3 | 0 | fully open | rain | moderate wind
BHGW0034 | 2019-01-29 10:38 | 25.1 | 22.2 | 0.9 | 51.8 | 981 | -1.07 | 0 | 0 | closed | rain | moderate wind
BHG010MB | 2019-01-29 10:39 | 51.4 | 35.5 | 0.4 | 12.7 | 981 | -26.68 | 2 | 0 | fully open | rain | moderate wind
BHGV0035 | 2019-01-29 10:42 | 51.6 | 37.9 | 0.3 | 10.2 | 981 | -0.52 | 1 | 0 | partially open | rain | moderate wind
BHGV0035 | 2019-01-29 10:43 | 50.7 | 37.9 | 0.2 | 11.2 | 981 | 1.31 | 1 | 0 | partially open | rain | moderate wind
BHGV0036 | 2019-01-29 10:44 | 71.1 | 33.1 | 0.4 | 0 | 981 | 2.08 | 3 | 0 | closed | rain | moderate wind
BHGV0036 | 2019-01-29 10:44 | 70.4 | 33.2 | 0.2 | 0 | 981 | 0.75 | 3 | 0 | partially open | rain | moderate wind
BHGV0037 | 2019-01-29 10:48 | 66.1 | 36.2 | 0.1 | 0 | 981 | 2.41 | 2 | 0 | closed | rain | moderate wind
BHGV0037 | 2019-01-29 10:48 | 65.9 | 36.4 | 0.1 | 0 | 981 | -0.33 | 2 | 2 | partially open | rain | moderate wind
BHM010MB | 2019-01-29 10:50 | 54.6 | 39.7 | 0.3 | 5.4 | 981 | -7.99 | 3 | 0 | fully open | rain | moderate wind
BHGV0018 | 2019-01-29 10:52 | 56.3 | 40.2 | 0.7 | 2.8 | 981 | -7.56 | 3 | 0 | partially open | rain | moderate wind
BHLC004B | 2019-01-29 10:54 | 48.7 | 36.6 | 3.2 | 11.5 | 981 | 1.34 | 3 | 0 | closed | rain | moderate wind
BHR0004B | 2019-01-29 10:56 | 50.3 | 37.3 | 0.6 | 11.8 | 981 | -7.07 | 1 | 0 | partially open | rain | moderate wind
BHR0004B | 2019-01-29 10:56 | 49.9 | 37.3 | 0.5 | 12.3 | 981 | -0.19 | 1 | 0 | partially open | rain | moderate wind
BHGV0015 | 2019-01-29 10:57 | 54.4 | 40 | 0.3 | 5.3 | 981 | -8.21 | 2 | 0 | fully open | rain | moderate wind
BHGV0014 | 2019-01-29 10:59 | 49.1 | 36.7 | 0.3 | 13.9 | 981 | -7.64 | 1 | 0 | fully open | rain | moderate wind
BHGV0013 | 2019-01-29 11:01 | 24.9 | 17.4 | 10.6 | 47.1 | 981 | 1.83 | 0 | 0 | closed | rain | moderate wind
BHGV0016 | 2019-01-29 11:02 | 20.9 | 12.4 | 13.6 | 53.1 | 981 | 1.72 | 0 | 0 | closed | rain | moderate wind
BHM010MA | 2019-01-29 11:05 | 52.8 | 39.3 | 0.5 | 7.4 | 981 | -8.47 | 2 | 0 | fully open | rain | moderate wind
BHGV0038 | 2019-01-29 11:07 | 67.4 | 36.7 | 0.3 | 0 | 981 | 2.61 | 2 | 0 | closed | rain | moderate wind
BHGV0038 | 2019-01-29 11:07 | 67.4 | 36.7 | 0.2 | 0 | 981 | -0.54 | 3 | 0 | partially open | rain | moderate wind
BHL000C4 | 2019-01-29 11:10 | 29.4 | 20.2 | 7.5 | 42.9 | 981 | 2.33 | 24 | 0 | closed | rain | moderate wind
BHGV0039 | 2019-01-29 11:13 | 53.5 | 32.8 | 0.5 | 13.2 | 981 | -1.43 | 1 | 0 | partially open | rain | moderate wind
BHGV0039 | 2019-01-29 11:13 | 52.6 | 32.8 | 0.6 | 14 | 981 | -0.11 | 1 | 0 | partially open | rain | moderate wind
BHGV0011 | 2019-01-29 11:15 | 55 | 27.7 | 0.7 | 16.6 | 982 | 2.64 | 1 | 0 | closed | rain | moderate wind
BHGV0011 | 2019-01-29 11:15 | 54.9 | 27.7 | 0.9 | 16.5 | 982 | -2.33 | 1 | 0 | partially open | rain | moderate wind
BHGV0010 | 2019-01-29 11:18 | 46.8 | 29.8 | 0.1 | 23.3 | 982 | 2.49 | 2 | 0 | closed | rain | moderate wind
BHGV0040 | 2019-01-29 11:20 | 53.6 | 34.3 | 0.1 | 12 | 982 | -6.62 | 2 | 0 | partially open | rain | moderate wind
BHGV0040 | 2019-01-29 11:20 | 53.1 | 34.5 | 0.2 | 12.2 | 982 | -0.04 | 2 | 0 | partially open | rain | moderate wind
BHLC001B | 2019-01-29 11:22 | 7 | 6.5 | 16.8 | 69.7 | 982 | 2.81 | 0 | 0 | closed | rain | moderate wind
BHGV0009 | 2019-01-29 11:23 | 54.6 | 30.3 | 0.7 | 14.4 | 982 | -7.11 | 1 | 0 | partially open | rain | moderate wind
BHGV0009 | 2019-01-29 11:23 | 53.4 | 30.9 | 0.4 | 15.3 | 982 | -7.62 | 2 | 0 | fully open | rain | moderate wind
BHGV0012 | 2019-01-29 11:28 | 58.3 | 39.9 | 0.7 | 1.1 | 981 | -6.13 | 2 | 0 | fully open | rain | moderate wind
BHGV0301 | 2019-01-29 11:31 | 61.7 | 33.7 | 1.3 | 3.3 | 981 | 4.43 | 3 | 0 | closed | rain | moderate wind
BHGV0301 | 2019-01-29 11:31 | 61.1 | 33.6 | 1.4 | 3.9 | 981 | 0.66 | 2 | 0 | partially open | rain | moderate wind
BHGV0046 | 2019-01-29 11:34 | 49.5 | 37.7 | 0.6 | 12.2 | 980 | -1.68 | 4 | 0 | partially open | rain | moderate wind
BHGV000A | 2019-01-29 11:36 | 59.8 | 42.8 | 0.3 | 0 | 980 | -2.4 | 3 | 0 | fully open | rain | moderate wind
BHGV0041 | 2019-01-29 11:38 | 56.4 | 37.1 | 0.7 | 5.8 | 981 | -4.13 | 2 | 0 | partially open | rain | moderate wind
BHGV0041 | 2019-01-29 11:38 | 56.1 | 37.4 | 0.2 | 6.3 | 981 | -5.08 | 2 | 0 | partially open | rain | moderate wind
BHGV0042 | 2019-01-29 11:43 | 70.9 | 30.9 | 0.6 | 0 | 982 | 3.71 | 2 | 0 | closed | rain | moderate wind
BHGV0042 | 2019-01-29 11:43 | 70.8 | 31 | 0.6 | 0 | 982 | -6.96 | 1 | 0 | partially open | rain | moderate wind
BHGV0043 | 2019-01-29 11:47 | 66.3 | 36.2 | 0.3 | 0 | 982 | 2.56 | 2 | 0 | closed | rain | moderate wind
BHGV0043 | 2019-01-29 11:47 | 66.3 | 36.4 | 0.3 | 0 | 982 | -6.5 | 3 | 0 | partially open | rain | moderate wind
BHGV0007 | 2019-01-29 11:49 | 72.5 | 30.4 | 0.5 | 0 | 982 | -0.11 | 2 | 0 | closed | rain | moderate wind
BHGV0007 | 2019-01-29 11:49 | 70.7 | 30.8 | 0.2 | 0 | 982 | -2.03 | 2 | 0 | partially open | rain | moderate wind
BHGV0008 | 2019-01-29 11:52 | 39.1 | 22.3 | 7 | 31.6 | 982 | 8.95 | 7 | 0 | closed | rain | moderate wind
BHLC002R | 2019-01-29 11:53 | 58 | 33 | 0.2 | 8.8 | 982 | -6.62 | 2 | 0 | partially open | rain | moderate wind
BHLC002R | 2019-01-29 11:54 | 57.8 | 33 | 0.1 | 9.1 | 982 | -0.02 | 2 | 0 | partially open | rain | moderate wind
BHGV0044 | 2019-01-29 11:56 | 58.5 | 32.9 | 0.4 | 8.2 | 982 | -6.14 | 1 | 0 | partially open | rain | moderate wind
BHGV0044 | 2019-01-29 11:56 | 58.1 | 33.1 | 0.4 | 8.4 | 982 | -1.36 | 2 | 0 | partially open | rain | moderate wind
BHGV0004 | 2019-01-29 12:00 | 48.1 | 28.1 | 1 | 22.8 | 982 | -35.52 | 1 | 0 | closed | rain | moderate wind
BHGV0003 | 2019-01-29 12:02 | 64.6 | 35 | 0.6 | 0 | 982 | -6.7 | 1 | 0 | fully open | rain | moderate wind
BHGV0006 | 2019-01-29 12:04 | 6.9 | 5.8 | 15.8 | 71.5 | 982 | 0.84 | 9 | 0 | closed | rain | moderate wind
BHGV0045 | 2019-01-29 12:06 | 55.1 | 37.5 | 0.6 | 6.8 | 982 | -6.39 | 2 | 0 | fully open | rain | moderate wind
BHGV0001 | 2019-01-29 12:09 | 0.1 | 1.5 | 19.5 | 78.9 | 982 | -0.23 | 0 | 0 | closed | rain | moderate wind
BHR0002B | 2019-01-29 12:15 | 53.5 | 37.6 | 2.2 | 6.7 | 981 | -1.65 | 3 | 0 | closed | rain | moderate wind
BHR0002B | 2019-01-29 12:15 | 53.3 | 37.7 | 2.3 | 6.7 | 981 | -2.42 | 3 | 0 | partially open | rain | moderate wind
BHGV0026 | 2019-01-29 12:20 | 58.5 | 32 | 3.7 | 5.8 | 981 | -4.85 | 1 | 0 | fully open | rain | moderate wind
BHGV0047 | 2019-01-29 12:23 | 54.3 | 25.5 | 1.4 | 18.8 | 981 | 1.07 | 2 | 0 | partially open | rain | moderate wind
BHGV0027 | 2019-01-29 12:26 | 58.6 | 39.2 | 1.1 | 1.1 | 981 | -5.27 | 2 | 0 | fully open | rain | moderate wind
BHGV000B | 2019-01-29 12:29 | 47.9 | 36.5 | 0.3 | 15.3 | 980 | -8.11 | 1 | 0 | partially open | rain | moderate wind
BHGV0030 | 2019-01-29 12:32 | 50.4 | 37.5 | 0.5 | 11.6 | 980 | -2.18 | 2 | 0 | fully open | rain | moderate wind
BHGV000C | 2019-01-29 12:34 | 57.9 | 42.5 | 0.7 | 0 | 980 | -4.74 | 3 | 0 | fully open | rain | moderate wind
BHGV0025 | 2019-01-29 12:38 | 39.9 | 28.8 | 1.5 | 29.8 | 982 | 2.08 | 0 | 0 | closed | rain | moderate wind
BHGV0024 | 2019-01-29 12:39 | 60.6 | 37.7 | 0.7 | 1 | 982 | -5.44 | 1 | 0 | fully open | rain | moderate wind
BHGV0048 | 2019-01-29 12:41 | 59.9 | 40.1 | 0.8 | 0 | 982 | -6.13 | 2 | 0 | partially open | rain | moderate wind
BHGV0048 | 2019-01-29 12:41 | 59.4 | 40.6 | 0.1 | 0 | 982 | -2.55 | 2 | 0 | fully open | rain | moderate wind
BHR0006B | 2019-01-29 12:45 | 56.1 | 38.2 | 1.4 | 4.3 | 981 | -3.67 | 1 | 0 | partially open | rain | moderate wind
BHR0006B | 2019-01-29 12:45 | 55.4 | 38.8 | 0.6 | 5.2 | 981 | -1.97 | 2 | 0 | partially open | rain | moderate wind
BHGV0033 | 2019-01-29 12:49 | 32 | 31.3 | 0.2 | 36.5 | 981 | -5.3 | 0 | 0 | partially open | rain | moderate wind
BHGV0033 | 2019-01-29 12:49 | 31.6 | 31.2 | 0.3 | 36.9 | 981 | -2.57 | 0 | 0 | closed | rain | moderate wind
BHGV0032 | 2019-01-29 12:51 | 60.2 | 42.2 | 0.7 | 0 | 981 | 2.04 | 2 | 0 | fully open | rain | moderate wind
BHG010MA | 2019-01-29 12:57 | 54.7 | 36.4 | 0.5 | 8.4 | 981 | -14.96 | 2 | 0 | fully open | rain | moderate wind
BHG01MDA | 2019-01-29 13:00 | 54.2 | 36.8 | 0.3 | 8.7 | 982 | 169.27 | 2 | 0 | fully open | rain | moderate wind

## February 2019
Date | 2019-02-07
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 16.8 | 83.1 | 0 | 0 | 989 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 16.5 | 83 | 0 | 0 | 990 | 0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 4 | 15.9 | 80.1 | 0 | 0 | 990 | -0.09 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 990 | 0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 16.2 | 83.2 | 0 | 0 | 990 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 16.3 | 83.4 | 0 | 0 | 989 | -0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.9 | 3.4 | 8.7 | 78 | 0 | 0 | 989 | 0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.9 | 9.3 | 11.3 | 62.5 | 0 | 0 | 989 | -0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 989 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.7 | 9.3 | 90 | 0 | 0 | 990 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2 | 9.3 | 88.7 | 0 | 0 | 989 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.6 | 16.3 | 82.1 | 0 | 0 | 990 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 16.8 | 82.8 | 0 | 0 | 990 | 0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 16.4 | 83.3 | 0 | 0 | 990 | 0.1 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 4.1 | 14 | 81.9 | 0 | 0 | 990 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 990 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 6.5 | 0.9 | 92.5 | 0 | 0 | 990 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 15.3 | 84.5 | 0 | 0 | 990 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 4.1 | 13.3 | 82.6 | 0 | 0 | 991 | -0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 15.9 | 81.9 | 0 | 0 | 990 | -0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 16.1 | 83.8 | 0 | 0 | 990 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.4 | 16.4 | 82.2 | 0 | 0 | 990 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2019-02-12
Weather: | dry
Wind conditions: | calm
Air Temperature: | 7 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 16.4 | 83.4 | 0 | 0 | 1015 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 17 | 82.7 | 0 | 0 | 1016 | 0.12 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 3.5 | 16.1 | 80.4 | 0 | 0 | 1016 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 1017 | -0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 16.4 | 83.4 | 0 | 0 | 1017 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 16.9 | 83 | 0 | 0 | 1016 | 0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.7 | 3.2 | 9.7 | 78.4 | 0 | 0 | 1017 | -0.13 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17.8 | 9.7 | 12.1 | 60.4 | 0 | 0 | 1017 | -0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 1017 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.5 | 9 | 90.5 | 0 | 0 | 1017 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.8 | 9.7 | 88.5 | 0 | 0 | 1017 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.2 | 82.5 | 0 | 0 | 1017 | 0.16 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.4 | 82.4 | 0 | 0 | 1016 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1016 | -0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 3.5 | 15.2 | 81.3 | 0 | 0 | 1016 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 1017 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.8 | 1.3 | 92.9 | 0 | 0 | 1017 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 15.9 | 83.8 | 0 | 0 | 1017 | 0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 4 | 13.8 | 82.2 | 0 | 0 | 1016 | 0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 16.4 | 81.7 | 0 | 0 | 1016 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 16.5 | 83.2 | 0 | 0 | 1016 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.5 | 16.6 | 81.9 | 0 | 0 | 1017 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2019-02-21
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | Gem 2000
Serial No: | GM12289
Calibrated To: | 2019-06-12
Operative | AS
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 16.5 | 83.2 | 0 | 0 | 1004 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 16.5 | 82.9 | 0 | 0 | 1004 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 3.3 | 16.9 | 79.8 | 0 | 0 | 1004 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.4 | 16.4 | 83.2 | 0 | 0 | 1004 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 15.8 | 84 | 0 | 0 | 1004 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 1004 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.6 | 3.4 | 9.8 | 77.2 | 0 | 0 | 1004 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 19.2 | 9.2 | 11.4 | 60.2 | 0 | 0 | 1004 | -0.1 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.2 | 16.2 | 82.5 | 0 | 0 | 1004 | -0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.4 | 9.4 | 90.2 | 0 | 0 | 1004 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.6 | 9.1 | 89.3 | 0 | 0 | 1004 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.1 | 15.2 | 83.7 | 0 | 0 | 1004 | -0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 16.5 | 83 | 0 | 0 | 1004 | 0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 1004 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 3.1 | 15.6 | 81.3 | 0 | 0 | 1004 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 17.9 | 81.8 | 0 | 0 | 1004 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.4 | 2 | 92.6 | 0 | 0 | 1004 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 15.2 | 84.5 | 0 | 0 | 1004 | -0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.3 | 14.9 | 81.8 | 0 | 0 | 1004 | 0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.6 | 16.5 | 81.9 | 0 | 0 | 1004 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 16 | 83.5 | 0 | 0 | 1004 | -0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 16.2 | 82.2 | 0 | 0 | 1004 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2019-02-27
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 16.8 | 83 | 0 | 0 | 1017 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 16.3 | 83.2 | 0 | 0 | 1017 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 3.1 | 16.6 | 80.3 | 0 | 0 | 1017 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 16.4 | 83.1 | 0 | 0 | 1017 | 0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 15.9 | 83.8 | 0 | 0 | 1018 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1016 | -0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.4 | 3.4 | 9.2 | 78 | 0 | 0 | 1017 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 19.1 | 10.2 | 11.2 | 59.5 | 0 | 0 | 1017 | -0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 1017 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.3 | 9.4 | 90.3 | 0 | 0 | 1017 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 9.3 | 89.2 | 0 | 0 | 1017 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1 | 15.7 | 83.3 | 0 | 0 | 1017 | -0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 16.9 | 82.8 | 0 | 0 | 1017 | 0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 1017 | 0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 3.2 | 15.8 | 81 | 0 | 0 | 1018 | 0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1017 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.5 | 1.6 | 92.9 | 0 | 0 | 1017 | 0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 15.6 | 84.2 | 0 | 0 | 1018 | -0.08 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.5 | 14.5 | 82 | 0 | 0 | 1017 | 0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.8 | 16.7 | 81.5 | 0 | 0 | 1017 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 16.2 | 83.4 | 0 | 0 | 1017 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 16.5 | 81.8 | 0 | 0 | 1018 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## March 2019
Date | 2019-03-08
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 16.4 | 83.2 | 0 | 0 | 972 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.8 | 16.1 | 83.1 | 0 | 0 | 973 | -0.2 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.8 | 16.3 | 80.9 | 0 | 0 | 971 | -0.13 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.8 | 15.8 | 83.4 | 0 | 0 | 972 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 15.4 | 84.2 | 0 | 0 | 973 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.6 | 16.5 | 82.9 | 0 | 0 | 972 | 0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.8 | 3.3 | 9.8 | 78.1 | 0 | 0 | 973 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.8 | 9.5 | 12.4 | 61.3 | 0 | 0 | 972 | -0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 972 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.5 | 8.9 | 90.6 | 0 | 0 | 972 | 0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.2 | 8.9 | 89.9 | 0 | 0 | 971 | 0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 15.2 | 83.4 | 0 | 0 | 973 | -0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 16.3 | 83.3 | 0 | 0 | 972 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 972 | 0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.9 | 15.4 | 81.7 | 0 | 0 | 972 | -0.1 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 17.3 | 82.4 | 0 | 0 | 972 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 6.3 | 1.4 | 92.3 | 0 | 0 | 972 | -0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.5 | 15.1 | 84.4 | 0 | 0 | 972 | -0.18 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.3 | 14.9 | 81.8 | 0 | 0 | 971 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 16.2 | 81.8 | 0 | 0 | 971 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 16 | 83.3 | 0 | 0 | 972 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 15.9 | 82 | 0 | 0 | 971 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2019-03-13
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17 | 82.8 | 0 | 0 | 990 | 0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 16.3 | 83.1 | 0 | 0 | 990 | -0.18 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.9 | 16.4 | 81.7 | 0 | 0 | 989 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 16.9 | 82.6 | 0 | 0 | 989 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 15.9 | 83.8 | 0 | 0 | 989 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 990 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.1 | 3.4 | 10.4 | 78.1 | 0 | 0 | 989 | -0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17.4 | 9.9 | 11.3 | 61.4 | 0 | 0 | 989 | 0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 989 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.3 | 9.5 | 90.2 | 0 | 0 | 990 | -0.32 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 9.1 | 90.1 | 0 | 0 | 989 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.1 | 16 | 82.9 | 0 | 0 | 990 | -0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.1 | 82.7 | 0 | 0 | 991 | 0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 991 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.2 | 16.1 | 81.7 | 0 | 0 | 990 | -0.18 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 990 | -0.2 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.9 | 2.2 | 91.9 | 0 | 0 | 990 | 0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 15.9 | 83.8 | 0 | 0 | 990 | -0.05 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.9 | 15.8 | 81.3 | 0 | 0 | 990 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.4 | 16.8 | 81.8 | 0 | 0 | 990 | -0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 16.4 | 83 | 0 | 0 | 990 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.8 | 16.6 | 81.6 | 0 | 0 | 991 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2019-03-20
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 16.7 | 83 | 0 | 0 | 1014 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 16.3 | 83.2 | 0 | 0 | 1016 | 0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.6 | 16.9 | 81.5 | 0 | 0 | 1015 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 16.6 | 82.8 | 0 | 0 | 1014 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 16.3 | 83.2 | 0 | 0 | 1015 | -0.8 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 16.5 | 83.3 | 0 | 0 | 1014 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.3 | 3.4 | 10.8 | 77.5 | 0 | 0 | 1015 | -0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.6 | 9.6 | 11.7 | 62.1 | 0 | 0 | 1014 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 1013 | -0.2 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.2 | 9.9 | 89.9 | 0 | 0 | 1015 | 0.13 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.6 | 9.4 | 90 | 0 | 0 | 1015 | -0.07 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.9 | 16.5 | 82.6 | 0 | 0 | 1016 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1015 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 1015 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.8 | 16.3 | 81.9 | 0 | 0 | 1015 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1015 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.5 | 2.9 | 91.6 | 0 | 0 | 1015 | -0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 16.3 | 83.5 | 0 | 0 | 1015 | 0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.5 | 15.9 | 81.6 | 0 | 0 | 1016 | -0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.6 | 17.1 | 81.3 | 0 | 0 | 1015 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 16.8 | 82.7 | 0 | 0 | 1015 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 16.8 | 81.6 | 0 | 0 | 1015 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12960 | MCERTS certified instrument
Date downloaded | 2019-03-01 19:32 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2019-02-27
Date of last factory calibration | 2018-11-15
Next service due | 2019-05-15
Date of last Gas Check | 2018-11-15
Security code | [55BBA804]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-03-01 08:32 | 47.9 | 35.3 | 0.7 | 16.1 | 1006 | 135.66 | 1 | 0
BHG010MB | 2019-03-01 08:35 | 48.1 | 35.6 | 0.6 | 15.7 | 1006 | -31.98 | 1 | 0
BHGV0035 | 2019-03-01 08:37 | 53.3 | 35.9 | 0.6 | 10.2 | 1005 | -0.89 | 0 | 0
BHGV0035 | 2019-03-01 08:38 | 52.5 | 36.7 | 0.5 | 10.3 | 1005 | -1.21 | 0 | 0
BHGV0036 | 2019-03-01 08:40 | 69.7 | 33.9 | 0.3 | 0 | 1005 | -1.68 | 1 | 0
BHGV0036 | 2019-03-01 08:40 | 68.9 | 34.4 | 0.2 | 0 | 1005 | -8.4 | 1 | 0
BHGV0037 | 2019-03-01 08:42 | 37.7 | 32.1 | 1.1 | 29.1 | 1005 | -0.5 | 1 | 0
BHM010MB | 2019-03-01 08:44 | 57.1 | 40.8 | 0.2 | 1.9 | 1005 | -8.81 | 3 | 0
BHGV0018 | 2019-03-01 08:46 | 59.9 | 42.2 | 0.5 | 0 | 1005 | -9.35 | 2 | 0
BHLC004B | 2019-03-01 08:47 | 4.5 | 7.6 | 14.6 | 73.3 | 1005 | 1.78 | 0 | 0
BHR0004B | 2019-03-01 08:50 | 54.1 | 40.3 | 0.1 | 5.5 | 1005 | -9.59 | 1 | 0
BHR0004B | 2019-03-01 08:50 | 53.6 | 40.9 | 0.1 | 5.4 | 1005 | -0.17 | 2 | 0
BHGV0015 | 2019-03-01 08:52 | 60.1 | 41.2 | 0.5 | 0 | 1005 | -9.48 | 2 | 0
BHGV0014 | 2019-03-01 08:53 | 52.4 | 38.9 | 0.2 | 8.5 | 1005 | -9.17 | 1 | 0
BHGV0013 | 2019-03-01 08:56 | 35.1 | 25.7 | 5.9 | 33.3 | 1005 | 0.91 | 0 | 0
BHGV0016 | 2019-03-01 08:57 | 16.9 | 12.4 | 12.9 | 57.8 | 1005 | 0.29 | 0 | 0
BHM010MA | 2019-03-01 08:59 | 56.9 | 40.4 | 0.6 | 2.1 | 1003 | -10.07 | 2 | 0
BHL000C4 | 2019-03-01 09:01 | 29 | 22.8 | 5.5 | 42.7 | 1005 | 2.08 | 28 | 0
BHGV0038 | 2019-03-01 09:02 | 35.1 | 27.4 | 1.1 | 36.4 | 1004 | -5.94 | 0 | 0
BHGV0038 | 2019-03-01 09:03 | 34.5 | 28.3 | 0.3 | 36.9 | 1004 | -0.99 | 0 | 0
BHGV0039 | 2019-03-01 09:04 | 47.7 | 30.6 | 0.4 | 21.3 | 1005 | -6.67 | 0 | 0
BHGV0011 | 2019-03-01 09:06 | 36.3 | 26.4 | 0.9 | 36.4 | 1005 | -2.86 | 0 | 0
BHGV0011 | 2019-03-01 09:06 | 36.3 | 26.9 | 0.2 | 36.6 | 1005 | 0.13 | 0 | 0
BHGV0010 | 2019-03-01 09:08 | 42.9 | 25.8 | 0.4 | 30.9 | 1006 | -1.38 | 0 | 0
BHGV0040 | 2019-03-01 09:10 | 35.2 | 30.7 | 0.4 | 33.7 | 1006 | -8.98 | 0 | 0
BHGV0040 | 2019-03-01 09:10 | 34.6 | 31.3 | 0.1 | 34 | 1006 | -0.11 | 0 | 0
BHLC001B | 2019-03-01 09:11 | 3.7 | 6 | 16.3 | 74 | 1006 | -3.67 | 0 | 0
BHGV0009 | 2019-03-01 09:13 | 40.7 | 30.9 | 0.2 | 28.2 | 1006 | -10.06 | 0 | 0
BHGV0009 | 2019-03-01 09:13 | 36.5 | 31.4 | 0.4 | 31.7 | 1006 | -1.32 | 1 | 0
BHGV0041 | 2019-03-01 09:16 | 54.8 | 37.4 | 0.2 | 7.6 | 1004 | -9.07 | 0 | 0
BHGV0041 | 2019-03-01 09:16 | 54.7 | 37.5 | 0.2 | 7.6 | 1004 | -9.38 | 0 | 0
BHGV0046 | 2019-03-01 09:18 | 51.6 | 39.1 | 0.6 | 8.7 | 1004 | -6.49 | 1 | 0
BHGV0046 | 2019-03-01 09:18 | 49.5 | 32.4 | 0.1 | 18 | 1004 | -0.76 | 2 | 0
BHR00003 | 2019-03-01 09:20 | 0.3 | 8.6 | 15.1 | 76 | 1004 | -9 | 0 | 0
BHR00003 | 2019-03-01 09:20 | 0.6 | 7.5 | 16.1 | 75.8 | 1004 | 0.5 | 0 | 0
BHGV0012 | 2019-03-01 09:22 | 58.2 | 40.4 | 0.6 | 0.8 | 1004 | -8.35 | 2 | 0
BHGV0042 | 2019-03-01 09:24 | 37.8 | 23.4 | 1 | 37.8 | 1004 | -6.65 | 0 | 0
BHGV0042 | 2019-03-01 09:24 | 36.9 | 24.2 | 0.7 | 38.2 | 1004 | -2.17 | 0 | 0
BHGV0043 | 2019-03-01 09:26 | 42 | 30.6 | 0.7 | 26.7 | 1006 | -4.47 | 0 | 0
BHGV0043 | 2019-03-01 09:26 | 41.4 | 30.7 | 0.7 | 27.2 | 1006 | -2.09 | 0 | 0
BHGV0007 | 2019-03-01 09:29 | 29.3 | 24.8 | 0.7 | 45.2 | 1005 | -7.89 | 1 | 0
BHGV0007 | 2019-03-01 09:29 | 29 | 25.4 | 0.7 | 44.9 | 1005 | -1.83 | 0 | 0
BHGV0008 | 2019-03-01 09:31 | 42.1 | 30.2 | 1.1 | 26.6 | 1005 | -18.04 | 1 | 0
BHLC002R | 2019-03-01 09:32 | 44.5 | 32.9 | 0.2 | 22.4 | 1005 | -10.83 | 0 | 0
BHGV0044 | 2019-03-01 09:34 | 43.5 | 32.6 | 0.4 | 23.5 | 1005 | -10.82 | 0 | 0
BHGV0044 | 2019-03-01 09:34 | 43.3 | 33 | 0.5 | 23.2 | 1005 | -1.07 | 0 | 0
BHGV0004 | 2019-03-01 09:39 | 50 | 29.6 | 0.3 | 20.1 | 1005 | -1.03 | 1 | 0
BHGV0004 | 2019-03-01 09:39 | 50.4 | 29.8 | 0.3 | 19.5 | 1005 | -1.25 | 1 | 0
BHGV0003 | 2019-03-01 09:46 | 62.6 | 35.7 | 0.8 | 0.9 | 1005 | -12.9 | 0 | 0
BHGV0006 | 2019-03-01 09:48 | 0.2 | 6.1 | 16.5 | 77.2 | 1005 | -3.03 | 0 | 0
BHGV0045 | 2019-03-01 09:52 | 57.3 | 36.2 | 0.8 | 5.7 | 1005 | -10.61 | 1 | 0
BHGV0001 | 2019-03-01 09:54 | 0.2 | 6.1 | 16.4 | 77.3 | 1005 | -1.56 | 0 | 0
BHR00001 | 2019-03-01 09:59 | 68.3 | 33.5 | 0.6 | 0 | 1004 | 4.98 | 0 | 0
BHR00001 | 2019-03-01 09:59 | 67 | 34.1 | 0.8 | 0 | 1004 | -11.17 | 0 | 0
BHR0001B | 2019-03-01 10:01 | 58.7 | 35.3 | 1.7 | 4.3 | 1004 | -0.89 | 0 | 0
BHR0001B | 2019-03-01 10:01 | 58.6 | 35.6 | 1.7 | 4.1 | 1004 | -1.51 | 1 | 0
BHGV0026 | 2019-03-01 10:05 | 59.3 | 35.8 | 0.4 | 4.5 | 1004 | -9.29 | 2 | 0
BHGV0027 | 2019-03-01 10:13 | 58 | 41.7 | 0 | 0.3 | 1003 | -8.85 | 2 | 0
BHGV0025 | 2019-03-01 10:18 | 40.8 | 30.4 | 0.4 | 28.4 | 1004 | -1.66 | 0 | 0
BHGV0024 | 2019-03-01 10:21 | 62.6 | 39.5 | 0 | 0 | 1005 | -9.34 | 0 | 0
BHGV0023 | 2019-03-01 10:24 | 0.1 | 3.4 | 16.7 | 79.8 | 1005 | 14.32 | 0 | 0
BHGV0048 | 2019-03-01 10:27 | 60.8 | 38.4 | 0.5 | 0.3 | 1005 | -10.74 | 1 | 0
BHGV0048 | 2019-03-01 10:27 | 60.1 | 38.9 | 1.3 | 0 | 1005 | -4.8 | 1 | 0
BHGV0028 | 2019-03-01 10:30 | 0 | 2.4 | 18.1 | 79.5 | 1003 | -3.66 | 0 | 0
BHGV0029 | 2019-03-01 10:31 | 56.9 | 35.2 | 0.4 | 7.5 | 1003 | -9.29 | 1 | 0
BHGV000C | 2019-03-01 10:33 | 59.9 | 42.4 | 0.3 | 0 | 1003 | -7.78 | 2 | 0
BHR00005 | 2019-03-01 10:35 | 12.5 | 12.2 | 3.3 | 72 | 1003 | 0.62 | 0 | 0
BHGV000B | 2019-03-01 10:37 | 51 | 33.3 | 0.6 | 15.1 | 1003 | -10.13 | 0 | 0
BHR00005 | 2019-03-01 10:39 | 50.9 | 36.1 | 0.6 | 12.4 | 1003 | -5.64 | 1 | 0
BHGV0031 | 2019-03-01 10:43 | 47.6 | 35.7 | 0.2 | 16.5 | 1003 | -7.83 | 1 | 0
BHLC0005 | 2019-03-01 10:45 | 53.5 | 40.2 | 1.4 | 4.9 | 1003 | -2.75 | 2 | 0
BHLC0005 | 2019-03-01 10:45 | 54.2 | 41.5 | 1.1 | 3.2 | 1003 | -4.62 | 2 | 0
BHLC006B | 2019-03-01 10:49 | 50.1 | 38.6 | 0.7 | 10.6 | 1003 | -5.5 | 0 | 0
BHLC0006 | 2019-03-01 10:52 | 62.5 | 40.1 | 0.3 | 0 | 1003 | -0.08 | 1 | 0
BHLC0006 | 2019-03-01 10:52 | 62.1 | 40.1 | 0.3 | 0 | 1003 | -2.2 | 1 | 0
BHGV0022 | 2019-03-01 10:54 | 77 | 28.5 | 0.7 | 0 | 1004 | 45.11 | 0 | 0
BHGV0049 | 2019-03-01 10:56 | 62.2 | 42.2 | 0 | 0 | 1004 | -2.02 | 3 | 0
BHGV0049 | 2019-03-01 10:57 | 59.8 | 41.6 | 0.2 | 0 | 1004 | -5.16 | 2 | 0
BHR0006B | 2019-03-01 10:59 | 56 | 39.4 | 0.1 | 4.5 | 1003 | -6.61 | 2 | 0
BHGV0033 | 2019-03-01 11:01 | 63.1 | 38.3 | 0.7 | 0 | 1003 | -1.93 | 2 | 0
BHGV0033 | 2019-03-01 11:01 | 60.1 | 39.8 | 0.3 | 0 | 1003 | -7.11 | 2 | 0
BHGV0032 | 2019-03-01 11:03 | 60.8 | 42.6 | 0.5 | 0 | 1003 | 3.45 | 2 | 0
BHPW0006 | 2019-03-01 11:06 | 0.5 | 14.2 | 15.4 | 69.9 | 1004 | 46.96 | 0 | 0
BHPW0005 | 2019-03-01 11:10 | 46.6 | 28.6 | 0.6 | 24.2 | 1004 | -8.29 | 0 | 0
BHPW0005 | 2019-03-01 11:10 | 46.4 | 28.6 | 0.7 | 24.3 | 1004 | -4.19 | 0 | 0
BHPW0004 | 2019-03-01 11:11 | 31.5 | 21.6 | 1 | 45.9 | 1004 | -6.59 | 0 | 0
BHPW0003 | 2019-03-01 11:13 | 21.7 | 18.9 | 2.2 | 57.2 | 1004 | -7.62 | 0 | 0
BHGW0034 | 2019-03-01 11:15 | 39.8 | 17.8 | 4.1 | 38.3 | 1004 | -0.4 | 3 | 0
BHPW0002 | 2019-03-01 11:16 | 1.3 | 8.7 | 15.2 | 74.8 | 1004 | 3.02 | 0 | 0
BHPW0001 | 2019-03-01 11:19 | 35.4 | 19 | 7.9 | 37.7 | 1004 | -8.92 | 0 | 0
BHG010MA | 2019-03-01 11:21 | 50 | 36.1 | 0.5 | 13.4 | 1004 | -23.29 | 1 | 0
BHG01MDA | 2019-03-01 11:23 | 49.8 | 36.2 | 0.6 | 13.4 | 1004 | 135.69 | 1 | 0

## April 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-04-03
Weather: | dry
Wind conditions: | calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.9 | 15.4 | 83.7 | 0 | 0 | 985 | -0.43 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1 | 16.5 | 82.5 | 0 | 0 | 986 | 0.2 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.2 | 15.2 | 82.6 | 0 | 0 | 985 | -0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 17.3 | 82.1 | 0 | 0 | 985 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 15.1 | 83.2 | 0 | 0 | 986 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.7 | 15.9 | 83.4 | 0 | 0 | 985 | -0.09 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.8 | 3.3 | 9.9 | 78 | 0 | 0 | 986 | -0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17.6 | 9.9 | 10.6 | 61.9 | 0 | 0 | 985 | -0.13 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.2 | 16.6 | 82.1 | 0 | 0 | 986 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.7 | 10.9 | 88.4 | 0 | 0 | 986 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 9.4 | 89.3 | 0 | 0 | 986 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.9 | 15.8 | 82.3 | 0 | 0 | 986 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 16.1 | 83.3 | 0 | 0 | 986 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.8 | 16.9 | 82.3 | 0 | 0 | 985 | 0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.8 | 15.9 | 82.3 | 0 | 0 | 985 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 986 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.5 | 3 | 91.5 | 0 | 0 | 986 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.5 | 15.3 | 84.2 | 0 | 0 | 986 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.8 | 15.8 | 81.4 | 0 | 0 | 985 | -0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.1 | 16.1 | 81.8 | 0 | 0 | 986 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 15.6 | 83.7 | 0 | 0 | 985 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.3 | 15.9 | 81.8 | 0 | 0 | 986 | 0.16 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-04-10
Weather: | dry
Wind conditions: | calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.8 | 15.2 | 84 | 0 | 0 | 992 | -0.23 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.2 | 16.2 | 82.6 | 0 | 0 | 992 | 0.21 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.3 | 15 | 82.7 | 0 | 0 | 992 | -0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 992 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.3 | 15 | 83.7 | 0 | 0 | 992 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.6 | 15.4 | 84 | 0 | 0 | 992 | -0.09 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.5 | 3.5 | 9.6 | 78.4 | 0 | 0 | 992 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17.4 | 8.8 | 10.4 | 63.4 | 0 | 0 | 992 | -0.13 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.4 | 16.4 | 82.1 | 0 | 0 | 992 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.5 | 10.8 | 88.7 | 0 | 0 | 992 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.1 | 9.6 | 89.3 | 0 | 0 | 992 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.6 | 15.5 | 82.9 | 0 | 0 | 992 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.7 | 16 | 83.3 | 0 | 0 | 992 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 15.9 | 83.6 | 0 | 0 | 992 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.7 | 15.4 | 82.9 | 0 | 0 | 992 | -0.1 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.6 | 17.9 | 81.5 | 0 | 0 | 992 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 5.2 | 3.2 | 91.6 | 0 | 0 | 992 | -0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.6 | 15.6 | 83.8 | 0 | 0 | 992 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.4 | 15.4 | 82.2 | 0 | 0 | 992 | -0.05 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 16.2 | 81.8 | 0 | 0 | 992 | 0.07 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.8 | 16.3 | 82.9 | 0 | 0 | 992 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.2 | 15.5 | 82.3 | 0 | 0 | 992 | 0.11 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-04-17
Weather: | dry
Wind conditions: | calm
Air Temperature: | 12 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.2 | 17.6 | 82.1 | 0 | 0 | 1003 | -0.33 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0.1 | 17.4 | 82.4 | 0 | 0 | 1003 | -0.35 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.2 | 15.4 | 82.4 | 0 | 0 | 1003 | -0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 16.2 | 83.2 | 0 | 0 | 1003 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 14 | 84.6 | 0 | 0 | 1003 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.7 | 15.9 | 83.4 | 0 | 0 | 1003 | -0.09 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.4 | 2.5 | 14.3 | 76.8 | 0 | 0 | 1003 | -0.63 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.9 | 6.6 | 14.9 | 66.6 | 0 | 0 | 1003 | -0.35 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.1 | 17.6 | 82.1 | 0 | 0 | 1004 | -0.35 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.6 | 8 | 90.3 | 0 | 0 | 1004 | -0.36 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.9 | 16.1 | 82.9 | 0 | 0 | 1003 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 15.2 | 83.4 | 0 | 0 | 1003 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.8 | 82.1 | 0 | 0 | 1003 | 0 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.3 | 17.7 | 81.9 | 0 | 0 | 1003 | 0 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 1.9 | 15.6 | 82.4 | 0 | 0 | 1002 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0 | 17.7 | 82.2 | 0 | 0 | 1002 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.3 | 5.4 | 93.2 | 0 | 0 | 1003 | -1.44 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.2 | 0.4 | 15.8 | 83.6 | 0 | 0 | 1003 | -0.23 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.8 | 15.6 | 83.5 | 0 | 0 | 1003 | 0.74 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 2.5 | 13 | 84.4 | 0 | 0 | 1003 | -0.17 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 17.6 | 82.3 | 0 | 0 | 1003 | -0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.6 | 16.4 | 81.9 | 0 | 0 | 1003 | -0.31 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-04-26
Weather: | dry
Wind conditions: | calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.3 | 18.1 | 81.5 | 0 | 0 | 989 | -0.12 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0.1 | 18.3 | 81.5 | 0 | 0 | 990 | -0.12 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.4 | 15.2 | 82.4 | 0 | 0 | 988 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 16.6 | 82.7 | 0 | 0 | 988 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.2 | 14.5 | 84.3 | 0 | 0 | 989 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.1 | 18.4 | 81.4 | 0 | 0 | 990 | -0.11 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.7 | 2.7 | 16.6 | 77 | 0 | 0 | 990 | -0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.6 | 7.2 | 14.5 | 66.7 | 0 | 0 | 989 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.1 | 18.4 | 81.4 | 0 | 0 | 991 | -0.1 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.3 | 12.7 | 85.9 | 0 | 0 | 987 | -0.27 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.1 | 16.6 | 82.2 | 0 | 0 | 987 | -0.49 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.5 | 15.7 | 82.8 | 0 | 0 | 988 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 18 | 81.8 | 0 | 0 | 986 | 0.42 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.4 | 18 | 81.5 | 0 | 0 | 986 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 1.9 | 16.2 | 81.8 | 0 | 0 | 986 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 18.1 | 81.7 | 0 | 0 | 986 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 0.7 | 16.3 | 82.8 | 0 | 0 | 988 | -0.13 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.3 | 0.5 | 15.9 | 83.3 | 0 | 0 | 988 | -0.22 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.4 | 17.9 | 81.6 | 0 | 0 | 986 | -0.01 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 0.2 | 18.1 | 81.6 | 0 | 0 | 988 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 18.3 | 81.5 | 0 | 0 | 989 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.6 | 17.8 | 81.5 | 0 | 0 | 989 | -0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12962 | MCERTS certified instrument
Date downloaded | 2019-04-26 18:26 | Software Version | 1.10.0
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2019-04-16
Date of last factory calibration | 2019-03-25
Next service due | 2019-09-25
Date of last Gas Check | 2019-03-25
Security code | [C156085F]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | CHOSEN 1 | CHOSEN 2 | CHOSEN 3 | SITECHOSEN 1 | SITECHOSEN 2 | SITECHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-04-26 08:52 | 44.5 | 34 | 0.5 | 21 | 986 | 153.19 | 1 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0035 | 2019-04-26 09:00 | 61.3 | 41.9 | 0.1 | 0 | 985 | 1.57 | 1 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0035 | 2019-04-26 09:01 | 60.9 | 42.2 | 0 | 0 | 985 | -4.4 | 2 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0036 | 2019-04-26 09:03 | 60.6 | 34.4 | 0 | 5 | 985 | -1.75 | 3 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0036 | 2019-04-26 09:03 | 60.1 | 34.1 | 0 | 5.8 | 985 | -2.53 | 4 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0037 | 2019-04-26 09:04 | 27 | 26 | 2.2 | 44.8 | 986 | -3.23 | 2 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHM010MB | 2019-04-26 09:05 | 59.5 | 39.3 | 0.5 | 0.7 | 985 | -16.56 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0018 | 2019-04-26 09:06 | 59.5 | 41.7 | 0 | 0 | 985 | -15.77 | 3 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHLC004B | 2019-04-26 09:07 | 13.5 | 11 | 9.3 | 66.2 | 985 | -0.41 | 2 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHR0004B | 2019-04-26 09:09 | 64 | 39.4 | 0 | 0 | 986 | 1.3 | 3 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHR0004B | 2019-04-26 09:10 | 64.1 | 39.9 | 0 | 0 | 986 | -3.22 | 3 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0015 | 2019-04-26 09:11 | 59 | 41.6 | 0 | 0 | 986 | -15.59 | 4 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0014 | 2019-04-26 09:12 | 56.1 | 37.6 | 0 | 6.3 | 986 | -17.04 | 3 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0014 | 2019-04-26 09:13 | 56.2 | 37.5 | 0 | 6.3 | 986 | -16.24 | 3 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0013 | 2019-04-26 09:14 | 20.3 | 16 | 10.2 | 53.5 | 986 | -0.23 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0016 | 2019-04-26 09:15 | 35.9 | 23 | 7.8 | 33.3 | 986 | -12.7 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHL000C4 | 2019-04-26 09:17 | 18.8 | 16.9 | 8.9 | 55.4 | 985 | -0.15 | 23 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0017 | 2019-04-26 09:20 | 63.8 | 39.4 | 0.5 | 0 | 985 | -10.89 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHM010MA | 2019-04-26 09:20 | 60 | 39.1 | 0.2 | 0.7 | 985 | -16.41 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0038 | 2019-04-26 09:21 | 28.9 | 28.2 | 0.9 | 42 | 985 | -10.37 | 2 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0038 | 2019-04-26 09:21 | 28.8 | 27.8 | 0.9 | 42.5 | 985 | 0.01 | 2 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0039 | 2019-04-26 09:22 | 33.9 | 26.5 | 0.6 | 39 | 986 | -13.32 | 1 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0039 | 2019-04-26 09:22 | 34 | 26.6 | 0.4 | 39 | 986 | -0.04 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0011 | 2019-04-26 09:24 | 25.2 | 19.2 | 0.4 | 55.2 | 986 | -2.61 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0010 | 2019-04-26 09:26 | 30.8 | 20.7 | 0.3 | 48.2 | 986 | -2.61 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0040 | 2019-04-26 09:30 | 63.2 | 33 | 1.5 | 2.3 | 986 | -1.42 | 2 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0040 | 2019-04-26 09:31 | 65.2 | 34.8 | 0.6 | 0 | 986 | -5.08 | 2 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHLC001B | 2019-04-26 09:32 | 16.8 | 12.6 | 10.8 | 59.8 | 986 | -0.16 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0009 | 2019-04-26 09:33 | 69.5 | 35.1 | 0.6 | 0 | 986 | -0.03 | 2 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0009 | 2019-04-26 09:34 | 66.7 | 37.4 | 0 | 0 | 986 | -11.66 | 3 | 0 | partially open |  |  | overcast | moderate wind
BHLC0003 | 2019-04-26 09:36 | 3.3 | 6.6 | 15.5 | 74.6 | 986 | -1.73 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0301 | 2019-04-26 09:38 | 19.3 | 14.4 | 10.8 | 55.5 | 985 | -15.92 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0301 | 2019-04-26 09:38 | 19.3 | 14.8 | 10.4 | 55.5 | 985 | -6.4 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0012 | 2019-04-26 09:40 | 55.1 | 38.1 | 0.6 | 6.2 | 985 | -15.67 | 1 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHR00003 | 2019-04-26 09:41 | 0.6 | 14.9 | 0.5 | 84 | 984 | -1.3 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0046 | 2019-04-26 09:44 | 60.5 | 43.5 | 0 | 0 | 984 | -6.22 | 3 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0046 | 2019-04-26 09:44 | 60.4 | 43.6 | 0 | 0 | 984 | -7.33 | 3 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0041 | 2019-04-26 09:51 | 44.5 | 35.2 | 0 | 20.3 | 984 | -12.64 | 1 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0042 | 2019-04-26 09:53 | 61.9 | 31.5 | 1.7 | 4.9 | 986 | -1.12 | 0 | 0 | partially open | vacuum increased |  | overcast | moderate wind
BHGV0042 | 2019-04-26 09:54 | 68.2 | 28.4 | 1.1 | 2.3 | 986 | -8.29 | 0 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0043 | 2019-04-26 09:57 | 48.8 | 32.7 | 0.5 | 18 | 986 | -0.32 | 1 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0043 | 2019-04-26 09:58 | 48.7 | 32.9 | 0.5 | 17.9 | 986 | -6.32 | 0 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0007 | 2019-04-26 09:59 | 28.1 | 26 | 0.9 | 45 | 986 | -10.28 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0007 | 2019-04-26 09:59 | 27.9 | 25.6 | 0.8 | 45.7 | 986 | -3.24 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0008 | 2019-04-26 10:01 | 3 | 3.9 | 16.6 | 76.5 | 986 | -0.08 | 2 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHLC002R | 2019-04-26 10:02 | 37.1 | 26.6 | 0.3 | 36 | 986 | -0.08 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0044 | 2019-04-26 10:04 | 7.9 | 16.2 | 3.2 | 72.7 | 985 | -1.28 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0044 | 2019-04-26 10:04 | 8 | 16.4 | 2.4 | 73.2 | 985 | -0.17 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0006 | 2019-04-26 10:11 | 0.1 | 2.8 | 17 | 80.1 | 986 | -5.24 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0003 | 2019-04-26 10:13 | 68.7 | 33.1 | 0.5 | 0 | 986 | -20.56 | 0 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0004 | 2019-04-26 10:14 | 23.5 | 20.6 | 0.6 | 55.3 | 986 | 1.14 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHR00001 | 2019-04-26 10:16 | 65 | 32.1 | 1.4 | 1.5 | 985 | -0.87 | 0 | 0 | partially open | vacuum increased |  | overcast | moderate wind
BHR00001 | 2019-04-26 10:17 | 63.7 | 32.3 | 1.3 | 2.7 | 985 | -19.69 | 0 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0001 | 2019-04-26 10:18 | 40.4 | 31.3 | 0.1 | 28.2 | 985 | -14.2 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0001 | 2019-04-26 10:18 | 40.3 | 31.3 | 0.3 | 28.1 | 985 | -7.21 | 0 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0045 | 2019-04-26 10:20 | 29 | 30.2 | 0.1 | 40.7 | 985 | -11.75 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0045 | 2019-04-26 10:21 | 29 | 30.3 | 0.1 | 40.6 | 985 | -0.02 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHLC002B | 2019-04-26 10:24 | 1.2 | 2.5 | 17.6 | 78.7 | 984 | -0.74 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHR0002B | 2019-04-26 10:26 | 67.7 | 31.2 | 1.1 | 0 | 984 | -0.31 | 4 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHR0002B | 2019-04-26 10:27 | 65.7 | 33.6 | 0.4 | 0.3 | 984 | -3.75 | 5 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0026 | 2019-04-26 10:28 | 52.2 | 34.5 | 0.1 | 13.2 | 984 | -21.13 | 4 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0047 | 2019-04-26 10:29 | 54.1 | 33.2 | 0.2 | 12.5 | 985 | -3.78 | 2 | 0 | partially open | vacuum increased |  | overcast | moderate wind
BHGV0047 | 2019-04-26 10:29 | 54.5 | 31.6 | 0 | 13.9 | 985 | -4.72 | 1 | 1 | partially open | no vacuum change |  | overcast | moderate wind
BHM050MB | 2019-04-26 10:31 | 52.2 | 37.4 | 0 | 10.4 | 985 | -23.46 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0025 | 2019-04-26 10:32 | 46 | 31.7 | 0 | 22.3 | 985 | -3.2 | 1 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0025 | 2019-04-26 10:32 | 46.5 | 32.2 | 0 | 21.3 | 985 | -5.16 | 1 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV000A | 2019-04-26 10:34 | 33.1 | 19.1 | 4.7 | 43.1 | 985 | 20.05 | 36 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0024 | 2019-04-26 10:35 | 65.7 | 38.8 | 0.1 | 0 | 985 | -23.56 | 4 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0023 | 2019-04-26 10:37 | 0.1 | 3.6 | 17.2 | 79.1 | 986 | -0.17 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0048 | 2019-04-26 10:39 | 56.8 | 34.4 | 0.6 | 8.2 | 986 | -21.7 | 0 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHM050MA | 2019-04-26 10:40 | 54.4 | 36 | 0.3 | 9.3 | 986 | -22.82 | 1 | 1 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0048 | 2019-04-26 10:41 | 61.6 | 42.7 | 0 | 0 | 985 | -9.29 | 2 | 1 | closed | vacuum increased |  | overcast | moderate wind
BHGV0048 | 2019-04-26 10:43 | 60.2 | 43.3 | 0 | 0 | 985 | -3.26 | 3 | 3 | partially open | no vacuum change |  | overcast | moderate wind
BHLC0006 | 2019-04-26 10:45 | 1.8 | 13 | 8.9 | 76.3 | 985 | -0.14 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHLC006B | 2019-04-26 10:46 | 59 | 38.6 | 1.2 | 1.2 | 984 | -9.28 | 0 | 0 | partially open | vacuum increased |  | overcast | moderate wind
BHLC006B | 2019-04-26 10:46 | 54.9 | 39.5 | 0.2 | 5.4 | 984 | -18.1 | 1 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHLC0005 | 2019-04-26 10:51 | 34.3 | 30.5 | 5.7 | 29.5 | 984 | 0.72 | 1 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0029 | 2019-04-26 10:52 | 56.3 | 37.5 | 0.8 | 5.4 | 984 | -21.72 | 1 | 1 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0028 | 2019-04-26 10:54 | 0.1 | 2.1 | 17.8 | 80 | 984 | -7.26 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0027 | 2019-04-26 10:57 | 54.5 | 37.5 | 0.5 | 7.5 | 985 | -19.8 | 0 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV000B | 2019-04-26 11:00 | 48.4 | 35.7 | 0.3 | 15.6 | 985 | -17.52 | 0 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHGV0030 | 2019-04-26 11:02 | 58.4 | 42 | 0 | 0 | 984 | -7.51 | 4 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV000C | 2019-04-26 11:03 | 55.9 | 41.5 | 0 | 2.6 | 984 | -11.35 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind
BHR00005 | 2019-04-26 11:05 | 9.1 | 14.1 | 0.5 | 76.3 | 984 | -0.27 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGV0031 | 2019-04-26 11:06 | 60.4 | 38.7 | 0.9 | 0 | 984 | -4.87 | 1 | 0 | closed | vacuum increased |  | overcast | moderate wind
BHGV0031 | 2019-04-26 11:07 | 60.4 | 40.6 | 0.1 | 0 | 984 | -8.68 | 3 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0033 | 2019-04-26 11:09 | 59.6 | 42.3 | 0 | 0 | 985 | -4.26 | 3 | 4 | partially open | vacuum increased |  | overcast | moderate wind
BHR0006B | 2019-04-26 11:09 | 62.3 | 40.5 | 1.9 | 0 | 984 | -0.57 | 2 | 0 | partially open | vacuum increased |  | overcast | moderate wind
BHR0006B | 2019-04-26 11:10 | 62.1 | 41.5 | 0 | 0 | 984 | -3.89 | 1 | 0 | partially open | no vacuum change |  | overcast | moderate wind
BHGV0049 | 2019-04-26 11:11 | 25.5 | 27.7 | 0.1 | 46.7 | 985 | -14.43 | 0 | 0 | partially open | vacuum decreased |  | overcast | moderate wind
BHGV0049 | 2019-04-26 11:11 | 25.6 | 26.9 | 0 | 47.5 | 985 | -0.06 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHPW0006 | 2019-04-26 11:12 | 0.3 | 6.5 | 13.3 | 79.9 | 985 | -5.22 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHPW0005 | 2019-04-26 11:14 | 32.7 | 21.1 | 2.6 | 43.6 | 985 | -20.54 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHPW0004 | 2019-04-26 11:15 | 25 | 17.5 | 2.8 | 54.7 | 985 | -14.09 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHPW0003 | 2019-04-26 11:16 | 16.3 | 14 | 5.3 | 64.4 | 985 | -19.59 | 0 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHPW0002 | 2019-04-26 11:18 | 29.5 | 24.9 | 1 | 44.6 | 986 | -0.84 | 3 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHGW0034 | 2019-04-26 11:20 | 28 | 16.2 | 3.5 | 52.3 | 986 | 0.5 | 3 | 0 | closed | no vacuum change |  | overcast | moderate wind
BHG01MDA | 2019-04-26 11:24 | 54.1 | 37.9 | 0.1 | 7.9 | 986 | 157.8 | 2 | 0 | fully open | no vacuum change |  | overcast | moderate wind

## May 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-05-01
Weather: | dry
Wind conditions: | calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1 | 19 | 80 | 0 | 0 | 1004 | 0.18 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1004 | 0.29 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.1 | 15.7 | 82.2 | 0 | 0 | 1005 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.9 | 19 | 80.1 | 0 | 0 | 1006 | -0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 1006 | -0.9 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.1 | 18.2 | 81.6 | 0 | 0 | 1004 | -0.09 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.8 | 3.3 | 15 | 76.9 | 0 | 0 | 1004 | 1.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 28.1 | 10.1 | 10.7 | 51.1 | 0 | 0 | 1005 | 0.45 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.2 | 18.6 | 81.1 | 0 | 0 | 1004 | -0.09 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 10.4 | 87.3 | 0 | 0 | 1004 | 1.58 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 17 | 81.5 | 0 | 0 | 1004 | 0.73 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.1 | 18.2 | 81.6 | 0 | 0 | 1005 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1004 | -1.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19.1 | 80.4 | 0 | 0 | 1004 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.2 | 13.9 | 83.9 | 0 | 0 | 1004 | 0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.9 | 17.2 | 80.9 | 0 | 0 | 1004 | 0.9 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 7.3 | 1.5 | 91.2 | 0 | 0 | 1004 | 0.5 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3.4 | 18.1 | 78.4 | 0 | 0 | 1004 | 0.47 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 5 | 13.6 | 81.3 | 0 | 0 | 1004 | 1 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.7 | 17.6 | 79.7 | 0 | 0 | 1004 | 0.16 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.4 | 18.7 | 79.9 | 0 | 0 | 1004 | 0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 17.5 | 80.8 | 0 | 0 | 1004 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-05-09
Weather: | dry
Wind conditions: | calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 19.2 | 79.6 | 0 | 0 | 1002 | 0.16 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 19.1 | 80.3 | 0 | 0 | 1002 | 0.26 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.3 | 15.4 | 82.3 | 0 | 0 | 1002 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 1002 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 1002 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.2 | 0.2 | 18.5 | 81.1 | 0 | 0 | 1002 | -0.07 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.6 | 3.2 | 15.4 | 76.8 | 0 | 0 | 1002 | 1 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 29 | 10 | 10.7 | 50.3 | 0 | 0 | 1002 | 0.42 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.4 | 18.9 | 80.5 | 0 | 0 | 1002 | -0.08 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.4 | 10.6 | 87 | 0 | 0 | 1002 | 1.46 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.6 | 17.2 | 81.2 | 0 | 0 | 1002 | 0.66 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.2 | 18.5 | 81.2 | 0 | 0 | 1002 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 1002 | -1.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 1002 | 0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.5 | 13.6 | 83.9 | 0 | 0 | 1002 | 0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.8 | 17.4 | 80.8 | 0 | 0 | 1002 | 0.14 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 7 | 16.9 | 76.1 | 0 | 0 | 1002 | 0.6 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3.2 | 18.4 | 78.3 | 0 | 0 | 1002 | 0.48 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 5.2 | 13.8 | 80.9 | 0 | 0 | 1002 | 1.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.8 | 17.2 | 80 | 0 | 0 | 1002 | 0.17 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.3 | 18.9 | 79.8 | 0 | 0 | 1002 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 17.6 | 80.8 | 0 | 0 | 1002 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-05-15
Weather: | dry
Wind conditions: | calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 18.7 | 81 | 0 | 0 | 1011 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 19 | 81 | 0 | 0 | 1012 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.4 | 15.6 | 82 | 0 | 0 | 1011 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 1013 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 1012 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 19.1 | 80.9 | 0 | 0 | 1011 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4 | 3.1 | 14.9 | 78 | 0 | 0 | 1011 | -0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.2 | 6.1 | 16.1 | 68.6 | 0 | 0 | 1011 | -0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.3 | 0.5 | 18.6 | 80.6 | 0 | 0 | 1011 | -0.07 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 14.7 | 84 | 0 | 0 | 1011 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.2 | 18.6 | 81.2 | 1 | 0 | 1010 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 18.5 | 81.2 | 0 | 0 | 1011 | -0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 19 | 81 | 0 | 0 | 1010 | 0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 18.9 | 81 | 1 | 0 | 1010 | -0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 1.9 | 15.9 | 81.6 | 0 | 0 | 1010 | -0.1 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 18.9 | 81.1 | 1 | 0 | 1009 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.6 | 16.4 | 82 | 0 | 0 | 1010 | 0.08 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3.5 | 18.6 | 77.8 | 0 | 0 | 1011 | 0.45 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.2 | 18.7 | 81.1 | 0 | 0 | 1010 | 0.05 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.6 | 17.1 | 80.3 | 0 | 0 | 1010 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 18.9 | 81 | 0 | 0 | 1010 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.5 | 16.6 | 80.9 | 0 | 0 | 1010 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-05-23
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 19.7 | 80 | 0 | 0 | 1001 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 19.6 | 80.1 | 0 | 0 | 1002 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.5 | 15.7 | 81.8 | 0 | 0 | 1001 | -0.05 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1002 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 18.5 | 81 | 0 | 0 | 1001 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 20 | 79.9 | 0 | 0 | 1002 | -0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.8 | 2.3 | 16.7 | 77.2 | 0 | 0 | 1002 | -0.09 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.5 | 6 | 16.4 | 68.1 | 0 | 0 | 1001 | -0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.6 | 18.7 | 80.5 | 0 | 0 | 1002 | -0.06 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.2 | 14.9 | 83.9 | 0 | 0 | 1002 | 0.3 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.1 | 17.4 | 81.5 | 0 | 0 | 1001 | 0.39 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1001 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 19.9 | 80 | 0 | 0 | 1001 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 20 | 79.8 | 0 | 0 | 1001 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.9 | 16.9 | 81.2 | 0 | 0 | 1001 | -0.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 20 | 79.9 | 0 | 0 | 1000 | -0.19 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1 | 15.8 | 83.2 | 0 | 0 | 1001 | 0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3.4 | 18.5 | 78 | 0 | 0 | 1001 | 0.41 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  |  | 0 | 0 |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.5 | 19.7 | 78.8 | 0 | 0 | 1001 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.8 | 16.8 | 80.4 | 0 | 0 | 1001 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 18.6 | 81.3 | 0 | 0 | 1001 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.8 | 17.6 | 79.6 | 0 | 0 | 1001 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-05-31
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1004 | 0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 1006 | 0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 1005 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 18.3 | 81 | 0 | 0 | 1004 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 19.9 | 79.6 | 0 | 0 | 1004 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 1006 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.4 | 1.6 | 14.7 | 80.3 | 0 | 0 | 1005 | 0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.4 | 2.2 | 16.9 | 77.5 | 0 | 0 | 1005 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.6 | 18.5 | 80.8 | 0 | 0 | 1004 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 6.8 | 90.9 | 0 | 0 | 1005 | 0.33 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.1 | 11.8 | 85.1 | 0 | 0 | 1005 | 0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 1005 | 0.09 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 1005 | 0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 1005 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 2.5 | 15.1 | 82.4 | 0 | 0 | 1005 | 0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 1004 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.1 | 9.5 | 88.4 | 0 | 0 | 1004 | 0.05 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3.2 | 18.6 | 78.1 | 0 | 0 | 1005 | 0.42 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 1.6 | 18.3 | 80 | 0 | 0 | 1004 | 0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4 | 16.2 | 79.8 | 0 | 0 | 1004 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 1004 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.6 | 17.3 | 80.1 | 0 | 0 | 1004 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12962 | MCERTS certified instrument
Date downloaded | 2019-05-23 19:12 | Software Version | 1.10.0
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2019-05-17
Date of last factory calibration | 2019-03-25
Next service due | 2019-09-25
Date of last Gas Check | 2019-03-25
Security code | [E6B61AE4]
ID | DATE | CH4 | CO2 | O2 | BALANCE | MIN O2 | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-05-23 09:13 | 51.1 | 33.7 | 0.4 | 14.8 | 0.4 | 1000 | 184.4 | 2 | 0
BHG010MB | 2019-05-23 09:15 | 51 | 33.8 | 0.3 | 14.9 | 0.3 | 999 | -9.41 | 3 | 0
BHG01MDB | 2019-05-23 09:15 | 51.1 | 33.7 | 0.3 | 14.9 | 0.3 | 999 | 188.86 | 3 | 0
BHPRG017 | 2019-05-23 09:21 | 50.9 | 33.4 | 1 | 14.7 |  | 999 | -0.08 | 1 | 0
BHM010MB | 2019-05-23 09:22 | 59.6 | 38.6 | 0.2 | 1.6 | 0.2 | 999 | -8.65 | 3 | 0
BHGV0018 | 2019-05-23 09:24 | 58.8 | 39.2 | 0 | 2 | 0 | 999 | -8.62 | 4 | 0
BHLC004B | 2019-05-23 09:28 | 20.9 | 4.5 | 4.8 | 69.8 | 0 | 999 | 0.93 | 3 | 0
BHR0004B | 2019-05-23 09:29 | 65.5 | 35.7 | 0.5 | 0 | 0.5 | 1000 | -0.03 | 2 | 0
BHR0004B | 2019-05-23 09:31 | 65 | 36.1 | 0.3 | 0 | 0.3 | 1000 | -8.47 | 2 | 0
BHGV0015 | 2019-05-23 09:31 | 58.6 | 36.7 | 0.4 | 4.3 | 0.4 | 999 | -8.51 | 3 | 0
BHGV0014 | 2019-05-23 09:33 | 32.4 | 29.6 | 0 | 38 | 0 | 999 | 0.02 | 1 | 0
BHGV0013 | 2019-05-23 09:35 | 12.7 | 9.6 | 14.3 | 63.4 | 0.1 | 999 | -0.03 | 1 | 0
BHGV0016 | 2019-05-23 09:37 | 48.2 | 31.1 | 4 | 16.7 | 4 | 999 | -0.01 | 3 | 0
BHGV0016 | 2019-05-23 09:38 | 53.3 | 33.7 | 2.5 | 10.5 | 2.6 | 999 | -8.34 | 3 | 0
BHM010MA | 2019-05-23 09:39 | 57.4 | 38.1 | 0.5 | 4 | 0.5 | 999 | -8.35 | 4 | 0
BHGV0038 | 2019-05-23 09:41 | 44.1 | 28.1 | 1.3 | 26.5 | 0.6 | 999 | -4.8 | 2 | 0
BHGV0039 | 2019-05-23 09:42 | 69.3 | 34.5 | 0.1 | 0 | 0.1 | 999 | 1.38 | 3 | 0
BHGV0039 | 2019-05-23 09:42 | 68.4 | 34.9 | 0 | 0 | 0 | 999 | -0.99 | 4 | 0
BHPRG039 | 2019-05-23 09:43 | 68.2 | 34.5 | 0.1 | 0 | 0.1 | 1000 | -1.52 | 5 | 0
BHGV0017 | 2019-05-23 09:44 | 63.6 | 34.9 | 0.7 | 0.8 | 0.1 | 999 | -8.17 | 3 | 0
BHR00003 | 2019-05-23 10:10 | 11.2 | 7.4 | 15.8 | 65.6 | 7.8 | 999 | 0.11 | 1 | 0
BHPRR003 | 2019-05-23 10:10 | 10.8 | 6.9 | 16 | 66.3 |  | 999 | 0.18 | 1 | 0
BHGV0046 | 2019-05-23 10:13 | 49.7 | 34.4 | 3.1 | 12.8 | 3.1 | 999 | -0.46 | 2 | 0
BHGV0046 | 2019-05-23 10:14 | 57.8 | 38.8 | 0.9 | 2.5 | 0.9 | 999 | -2.58 | 4 | 0
BHPRG046 | 2019-05-23 10:14 | 58.4 | 39.6 | 0.8 | 1.2 |  | 998 | 0.09 | 3 | 0
BHLC0003 | 2019-05-23 10:17 | 45.8 | 29.6 | 4.4 | 20.2 | 1 | 999 | -0.62 | 3 | 0
BHPRL003 | 2019-05-23 10:18 | 46 | 29.6 | 4.4 | 20 |  | 999 | 0.11 | 2 | 0
BHGV0301 | 2019-05-23 10:19 | 64.7 | 36.7 | 0.3 | 0 | 0.4 | 999 | -7.08 | 3 | 0
BHGV0040 | 2019-05-23 10:22 | 66.2 | 35.4 | 0.2 | 0 | 0.2 | 999 | -7.45 | 3 | 0
BHGV0009 | 2019-05-23 10:23 | 53.9 | 30 | 0 | 16.1 | 0 | 1000 | -7.16 | 3 | 0
BHLC001B | 2019-05-23 10:26 | 10.2 | 7.5 | 15.4 | 66.9 |  | 1000 | 0.17 | 1 | 0
BHGV0042 | 2019-05-23 10:28 | 74.5 | 29.7 | 0.1 | 0 | 0.1 | 1000 | 1.85 | 2 | 0
BHGV0042 | 2019-05-23 10:30 | 67.7 | 29.1 | 1.1 | 2.1 | 0.7 | 1000 | -1.55 | 2 | 0
BHPRG042 | 2019-05-23 10:30 | 67.8 | 28.6 | 1.2 | 2.4 |  | 1000 | -1.79 | 1 | 0
BHGV0043 | 2019-05-23 10:32 | 44.9 | 28 | 0.2 | 26.9 | 0.2 | 999 | -2.37 | 2 | 0
BHGV0043 | 2019-05-23 10:33 | 45 | 28 | 0.2 | 26.8 |  | 999 | -1.78 | 2 | 0
BHGV0007 | 2019-05-23 10:34 | 65.7 | 25.8 | 1.7 | 6.8 | 0.3 | 999 | -0.26 | 1 | 0
BHGV0007 | 2019-05-23 10:35 | 67.8 | 25.8 | 1.2 | 5.2 | 1.2 | 999 | -2.73 | 2 | 0
BHGV0008 | 2019-05-23 10:37 | 16.4 | 10.1 | 13 | 60.5 | 1.1 | 999 | 1.05 | 12 | 0
BHLC002R | 2019-05-23 10:38 | 0.1 | 2.4 | 18.9 | 78.6 | 11.8 | 999 | 0.23 | 0 | 0
BHGV0044 | 2019-05-23 10:42 | 29.7 | 23.8 | 0.7 | 45.8 | 0.4 | 999 | -2.53 | 2 | 0
BHPRG044 | 2019-05-23 10:43 | 29.4 | 23.4 | 0.8 | 46.4 |  | 999 | 0.21 | 2 | 0
BHGV0004 | 2019-05-23 10:45 | 53.1 | 26.4 | 0.3 | 20.2 | 0.3 | 999 | 0.2 | 2 | 0
BHGV0004 | 2019-05-23 10:46 | 52.8 | 26.7 | 0.3 | 20.2 | 0.3 | 999 | -0.86 | 2 | 0
BHGV0003 | 2019-05-23 10:48 | 70.4 | 32.5 | 0 | 0 | 0 | 999 | -6.67 | 2 | 0
BHLC002B | 2019-05-23 10:52 | 0.2 | 2.7 | 18.8 | 78.3 | 12.7 | 999 | -0.87 | 2 | 0
BHGV0006 | 2019-05-23 10:53 | 0.1 | 1.2 | 19.4 | 79.3 | 18.8 | 999 | -0.27 | 0 | 0
BHR00001 | 2019-05-23 10:56 | 29.4 | 16 | 6.1 | 48.5 | 6.1 | 998 | -6.46 | 1 | 0
BHR0001B | 2019-05-23 10:57 | 57.9 | 29.8 | 0.5 | 11.8 | 0.6 | 998 | -2.22 | 2 | 0
BHR0001B | 2019-05-23 10:57 | 49 | 30.5 | 0.2 | 20.3 |  | 998 | -4.02 | 2 | 0
BHGV0045 | 2019-05-23 10:59 | 64.8 | 37.6 | 0 | 0 | 0 | 997 | 0.76 | 3 | 0
BHGV0045 | 2019-05-23 10:59 | 64.9 | 37.7 | 0 | 0 |  | 997 | -1.87 | 3 | 0
BHPRG045 | 2019-05-23 11:00 | 64.4 | 37.5 | 0.1 | 0 |  | 997 | 0.13 | 3 | 0
BHLC002B | 2019-05-23 11:01 | 62.5 | 39.5 | 0 | 0 | 0 | 997 | 1.77 | 3 | 0
BHLC002B | 2019-05-23 11:03 | 62.3 | 39.6 | 0.1 | 0 |  | 997 | 0.74 | 3 | 0
BHGV0026 | 2019-05-23 11:05 | 51.2 | 33.6 | 0 | 15.2 | 0 | 997 | -5.25 | 3 | 0
BHR0002B | 2019-05-23 11:06 | 64.4 | 30.4 | 0.6 | 4.6 | 0 | 997 | 0.31 | 8 | 0
BHR0002B | 2019-05-23 11:06 | 64.2 | 29.8 | 0.6 | 5.4 |  | 997 | 2.49 | 7 | 0
BHGV0028 | 2019-05-23 11:09 | 0.3 | 6.4 | 17.6 | 75.7 | 0.7 | 997 | -1.29 | 3 | 0
BHM050MB | 2019-05-23 11:10 | 54 | 31.3 | 0.5 | 14.2 | 0.5 | 998 | -5.93 | 2 | 0
BHGV0025 | 2019-05-23 11:12 | 50.4 | 31.6 | 0.2 | 17.8 | 0.2 | 998 | -0.36 | 3 | 0
BHGV0025 | 2019-05-23 11:12 | 50.8 | 31.3 | 0.2 | 17.7 |  | 998 | -0.93 | 2 | 0
BHGV0024 | 2019-05-23 11:14 | 59.4 | 36.1 | 0 | 4.5 | 0 | 998 | -5.82 | 2 | 0
BHGV000A | 2019-05-23 11:16 | 37.1 | 23 | 4 | 35.9 | 0 | 998 | 9.36 | 28 | 0
BHGV0048 | 2019-05-23 11:17 | 60.7 | 35.8 | 0.7 | 2.8 | 0.8 | 998 | -5.7 | 19 | 0
BHM050MA | 2019-05-23 11:18 | 52.4 | 36.3 | 0.1 | 11.2 | 0.1 | 998 | -6 | 7 | 0
BHPRG048 | 2019-05-23 11:19 | 52.4 | 35.7 | 0.5 | 11.4 |  | 997 | 0.21 | 3 | 0
BHLC0006 | 2019-05-23 11:21 | 2.3 | 18 | 9.7 | 70 | 0.3 | 997 | 0.24 | 2 | 0
BHLC006B | 2019-05-23 11:22 | 69.6 | 32.8 | 0.6 | 0 | 0.8 | 997 | 1.43 | 2 | 0
BHLC006B | 2019-05-23 11:23 | 67.1 | 34.9 | 0.2 | 0 |  | 997 | -1.2 | 2 | 0
BHLC0005 | 2019-05-23 11:24 | 7 | 18.9 | 7.7 | 66.4 | 0.6 | 996 | 0.19 | 3 | 0
BHGV0029 | 2019-05-23 11:25 | 54.1 | 31.4 | 0.4 | 14.1 | 0.4 | 996 | -4.01 | 2 | 0
BHGV000C | 2019-05-23 11:27 | 57.5 | 38.3 | 0 | 4.2 | 0 | 997 | -2.15 | 4 | 0
BHR00005 | 2019-05-23 11:29 | 9.3 | 21.4 | 0.9 | 68.4 | 0.2 | 996 | 0.49 | 3 | 0
BHPRL005 | 2019-05-23 11:29 | 8.4 | 16.6 | 0.7 | 74.3 | 0.7 | 996 | 0.29 | 2 | 0
BHGV0031 | 2019-05-23 11:30 | 58.4 | 31.3 | 0.5 | 9.8 | 0.5 | 997 | -1.85 | 2 | 0
BHGV0031 | 2019-05-23 11:31 | 57.2 | 33.6 | 0 | 9.2 | 0 | 997 | -4.81 | 2 | 0
BHGV0033 | 2019-05-23 11:32 | 40.6 | 29.4 | 0 | 30 | 0 | 997 | -2.52 | 2 | 0
BHR0006B | 2019-05-23 11:33 | 63.7 | 38.3 | 0 | 0 | 0 | 997 | -1.28 | 3 | 0
BHR0006B | 2019-05-23 11:34 | 62.5 | 39.1 | 0 | 0 | 0 | 997 | -1.22 | 3 | 0
BHPRR06B | 2019-05-23 11:34 | 62 | 39.4 | 0 | 0 |  | 997 | -1.43 | 3 | 0
BHGV0049 | 2019-05-23 11:36 | 55.7 | 34.5 | 1.8 | 8 | 0 | 997 | 0.44 | 3 | 0
BHGV0049 | 2019-05-23 11:36 | 59.2 | 36.9 | 0.5 | 3.4 | 0.5 | 997 | -1.84 | 3 | 0
BHPRG049 | 2019-05-23 11:36 | 60.1 | 37.4 | 0.5 | 2 |  | 997 | 0.17 | 3 | 0
BHPW0002 | 2019-05-23 11:37 | [5 empty] | 997 | 0.22 | 4 | 0
BHGW0034 | 2019-05-23 11:41 | 17.9 | 16.6 | 3.6 | 61.9 | 0 | 997 | 0.23 | 2 | 0
BHG010MA | 2019-05-23 11:43 | 54.6 | 33 | 0.4 | 12 | 0.4 | 998 | -5.56 | 3 | 0
BHG01MDA | 2019-05-23 11:43 | 53.9 | 33.9 | 0.3 | 11.9 | 0.3 | 998 | 189.71 | 3 | 0
BHG01MDA | 2019-05-23 11:46 | 54.1 | 34.3 | 0.1 | 11.5 | 0.1 | 998 | 184.57 | 3 | 0

## June 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-06-05
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1 | 18.6 | 80.4 | 0 | 0 | 991 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 992 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 991 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 18.3 | 81.1 | 0 | 0 | 991 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 18.8 | 80.7 | 0 | 0 | 993 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 992 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.6 | 1.2 | 17.7 | 78.5 | 0 | 0 | 992 | 0 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.1 | 2.2 | 16.9 | 77.8 | 0 | 0 | 991 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.6 | 18.5 | 80.8 | 0 | 0 | 991 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 6.8 | 90.9 | 0 | 0 | 991 | 0.33 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.8 | 13.8 | 84.4 | 0 | 0 | 992 | 0.81 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.7 | 18.8 | 80.4 | 0 | 0 | 992 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 992 | 0.99 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 992 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.9 | 14.4 | 83.7 | 0 | 0 | 992 | 0.64 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.9 | 15.9 | 83.2 | 0 | 0 | 992 | 0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.3 | 10.6 | 88.1 | 0 | 0 | 991 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3 | 18.4 | 78.5 | 0 | 0 | 991 | 0.42 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0 | 18.5 | 81.4 | 0 | 0 | 991 | -0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.6 | 16.9 | 80.5 | 0 | 0 | 991 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  |  |  |  | 100 | 0 | 0 |  |  | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.3 | 17.1 | 80.6 | 0 | 0 | 991 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-06-12
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.3 | 18 | 80.7 | 0 | 0 | 1001 | 0.15 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1001 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1002 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 18.3 | 81.1 | 0 | 0 | 1001 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 18.8 | 80.7 | 0 | 0 | 1002 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 1001 | 0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.9 | 1.5 | 16.3 | 78.3 | 0 | 0 | 1002 | -0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.1 | 2.2 | 16.9 | 77.8 | 0 | 0 | 1001 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.6 | 18.5 | 80.8 | 0 | 0 | 1002 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 6.8 | 90.9 | 0 | 0 | 1001 | 0.33 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 15.1 | 83.6 | 0 | 0 | 1003 | -0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 1001 | -0.1 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 18.5 | 80.9 | 0 | 0 | 1001 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 1003 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.5 | 15 | 83.5 | 0 | 0 | 1002 | 0.16 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.7 | 16.7 | 82.6 | 0 | 0 | 1002 | 0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 11.2 | 87.4 | 0 | 0 | 1002 | -0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 3 | 18.4 | 78.5 | 0 | 0 | 1001 | 0.42 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.2 | 18.2 | 81.6 | 0 | 0 | 1002 | -0.16 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 16.6 | 81.2 | 0 | 0 | 1001 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 1001 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2 | 16.7 | 81.3 | 0 | 0 | 1002 | -0.19 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-06-20
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GA2000Plus
Serial No: | GA12960
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.4 | 17.8 | 80.8 | 0 | 0 | 996 | 0.19 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 18.8 | 81 | 0 | 0 | 997 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 996 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 18.2 | 81.3 | 0 | 0 | 996 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 18.6 | 80.9 | 0 | 0 | 996 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 997 | 0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.4 | 3.5 | 14.4 | 76.7 | 0 | 0 | 996 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.1 | 2.2 | 16.9 | 77.8 | 0 | 0 | 996 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.6 | 18.5 | 80.8 | 0 | 0 | 996 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.3 | 6.8 | 90.9 | 0 | 0 | 997 | 0.29 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1 | 16.2 | 82.8 | 0 | 0 | 996 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.2 | 81.4 | 0 | 0 | 996 | 0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 18.4 | 81.3 | 0 | 0 | 995 | -0.12 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 996 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 15.7 | 83.1 | 0 | 0 | 996 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 996 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 11.8 | 87.1 | 0 | 0 | 996 | -0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.5 | 18.2 | 79.3 | 0 | 0 | 996 | 0.39 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  |  | 0 | 0 |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.5 | 17.8 | 81.7 | 0 | 0 | 996 | -0.11 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.6 | 16.1 | 81.3 | 0 | 0 | 996 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 996 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.5 | 17.3 | 81.2 | 0 | 0 | 995 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-06-26
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 16.6 | 82.9 | 0 | 0 | 1014 | -0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 18.9 | 80.6 | 0 | 0 | 1012 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.1 | 80.6 | 0 | 0 | 1013 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 1014 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 18.5 | 81.1 | 0 | 0 | 1014 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19 | 80.8 | 0 | 0 | 1013 | -0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3 | 1.6 | 12.6 | 82.8 | 0 | 0 | 1014 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.3 | 2.4 | 16.5 | 77.8 | 0 | 0 | 1014 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.7 | 18.4 | 80.7 | 0 | 0 | 1014 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0 | 17.1 | 82.8 | 0 | 0 | 1014 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.5 | 13.3 | 84.1 | 0 | 0 | 1014 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.2 | 17 | 82.7 | 0 | 0 | 1014 | 0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.1 | 82.8 | 0 | 0 | 1013 | 0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 1013 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 15.6 | 83.3 | 0 | 0 | 1013 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 17.1 | 82.7 | 0 | 0 | 1013 | 0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 0.9 | 16.5 | 82.4 | 0 | 0 | 1013 | 0.13 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.4 | 18.4 | 79.2 | 0 | 0 | 1014 | 0.27 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.6 | 82 | 0 | 0 | 1014 | -0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.2 | 1.6 | 14.8 | 83.4 | 0 | 0 | 1013 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 18.6 | 81.2 | 0 | 0 | 1013 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 2 | 15.3 | 82.6 | 0 | 0 | 1013 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## July 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-07-03
Weather: | dry
Wind conditions: | calm
Air Temperature: | 18 | OC
Instrument: | GA2000Plus
Serial No: | GA12598
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.8 | 17.1 | 82.1 | 0 | 0 | 1011 | -0.15 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 18.7 | 80.8 | 0 | 0 | 1011 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19 | 80.8 | 0 | 0 | 1012 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 1011 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 18.3 | 81.4 | 0 | 0 | 1011 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 1011 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.3 | 3.2 | 14.9 | 77.6 | 0 | 0 | 1012 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.6 | 2.2 | 16.8 | 77.4 | 0 | 0 | 1011 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.3 | 0.7 | 18.1 | 80.9 | 0 | 0 | 1011 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0 | 17.6 | 82.2 | 0 | 0 | 1011 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 15.4 | 83.1 | 0 | 0 | 1012 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 1011 | -0.11 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1011 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 1011 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1 | 15.4 | 83.6 | 0 | 0 | 1011 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 1012 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1 | 13.2 | 85.7 | 0 | 0 | 1012 | 0.05 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.2 | 18.3 | 79.5 | 0 | 0 | 1011 | 0.25 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.3 | 17.9 | 81.8 | 0 | 0 | 1012 | -0.11 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 15.4 | 82.7 | 0 | 0 | 1012 | -0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.4 | 81.3 | 0 | 0 | 1011 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 16.4 | 81.9 | 0 | 0 | 1012 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-07-10
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12598
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.1 | 16.5 | 82.1 | 0 | 0 | 1004 | 0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 18.7 | 80.8 | 0 | 0 | 1004 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 1004 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 18.6 | 81.2 | 0 | 0 | 1004 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 18.2 | 81.7 | 0 | 0 | 1004 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 1004 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.9 | 3.3 | 15.8 | 77.6 | 0 | 0 | 1004 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.4 | 2.1 | 16.5 | 78 | 0 | 0 | 1004 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.6 | 18 | 81.2 | 0 | 0 | 1004 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0 | 17.5 | 82.2 | 0 | 0 | 1004 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.8 | 16.1 | 83.1 | 0 | 0 | 1004 | -0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 16.9 | 82.3 | 0 | 0 | 1003 | -0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.2 | 82.2 | 0 | 0 | 1003 | -0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 1004 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 15.5 | 83.4 | 0 | 0 | 1003 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.5 | 17.9 | 82.2 | 0 | 0 | 1004 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 12.7 | 86.2 | 0 | 0 | 1004 | -0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.1 | 18.2 | 79.7 | 0 | 0 | 1004 | 0.24 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 1004 | -0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.7 | 16.3 | 82 | 0 | 0 | 1004 | -0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 1004 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.8 | 15.9 | 82.3 | 0 | 0 | 1003 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-07-16
Weather: | dry
Wind conditions: | calm
Air Temperature: | 17 | OC
Instrument: | GA2000Plus
Serial No: | GA12598
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.5 | 15.7 | 82.8 | 0 | 0 | 1002 | -0.13 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 18.5 | 81.1 | 0 | 0 | 1002 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 1002 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 18.5 | 81.2 | 0 | 0 | 1003 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 18.2 | 81.6 | 0 | 0 | 1002 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 1002 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.9 | 3.2 | 15.1 | 75.8 | 0 | 0 | 1003 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.6 | 2.2 | 16.6 | 77.6 | 0 | 0 | 1003 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 0.7 | 18.2 | 81 | 0 | 0 | 1003 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0 | 17.4 | 82.4 | 0 | 0 | 1003 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 15.6 | 82.9 | 0 | 0 | 1002 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.9 | 17.3 | 81.8 | 0 | 0 | 1003 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.7 | 82 | 0 | 0 | 1003 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19 | 80.5 | 0 | 0 | 1003 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1 | 15.4 | 83.6 | 0 | 0 | 1003 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 1003 | -0.1 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 12.1 | 86.5 | 0 | 0 | 1003 | -0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.3 | 18 | 79.7 | 0 | 0 | 1003 | 0.22 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1003 | -0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 16 | 81.8 | 0 | 0 | 1003 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.4 | 81.3 | 0 | 0 | 1003 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2 | 16.1 | 81.9 | 0 | 0 | 1002 | -0.16 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-07-26
Weather: | dry
Wind conditions: | calm
Air Temperature: | 15 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.7 | 19.6 | 79.6 | 0 | 0 | 990 | 0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0 | 20.2 | 79.7 | 0 | 0 | 992 | 0.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.8 | 79.9 | 0 | 0 | 990 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 18.6 | 81.2 | 0 | 0 | 990 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 18.7 | 80.8 | 0 | 0 | 990 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 19.5 | 80.2 | 0 | 0 | 990 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.8 | 3.5 | 15.2 | 75.5 | 0 | 0 | 990 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.9 | 2.1 | 16.7 | 77.3 | 0 | 0 | 990 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.6 | 18.5 | 80.7 | 0 | 0 | 990 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0 | 17.6 | 82.1 | 0 | 0 | 990 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 15.8 | 82.7 | 0 | 0 | 990 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 17.5 | 81.7 | 0 | 0 | 990 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 990 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 990 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 15.6 | 83.3 | 0 | 0 | 990 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 17 | 82.6 | 0 | 0 | 990 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 5.1 | 9.4 | 85.4 | 0 | 0 | 990 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.4 | 18.4 | 79.2 | 0 | 0 | 990 | 0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 990 | -0.08 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 16.2 | 81.4 | 0 | 0 | 990 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 18.2 | 81.4 | 0 | 0 | 990 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 2.1 | 15 | 82.8 | 0 | 0 | 990 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-07-31
Weather: | dry
Wind conditions: | calm
Air Temperature: | 15 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.6 | 20.1 | 79.3 | 0 | 0 | 988 | 0.14 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 20.6 | 79.4 | 0 | 0 | 989 | 0.14 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.2 | 80.7 | 0 | 0 | 989 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.1 | 19 | 80.8 | 0 | 0 | 989 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 19.1 | 80.2 | 0 | 0 | 989 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.4 | 19.4 | 84 | 0 | 0 | 989 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.6 | 3.2 | 15.6 | 75 | 0 | 0 | 989 | 0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3 | 2.2 | 16.2 | 76.2 | 0 | 0 | 989 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.4 | 0.7 | 18.6 | 81 | 0 | 0 | 989 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0 | 17.9 | 84 | 0 | 0 | 989 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.4 | 15.9 | 81 | 0 | 0 | 989 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.7 | 17.6 | 81.8 | 0 | 0 | 989 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 17.5 | 80.1 | 0 | 0 | 989 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 19.4 | 83.6 | 0 | 0 | 989 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 15.7 | 78.4 | 0 | 0 | 989 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 20.4 | 79.5 | 0 | 0 | 989 | 0.1 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 6.2 | 7.9 | 85.9 | 0 | 0 | 989 | 0.27 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.1 | 18.6 | 97.9 | 0 | 0 | 989 | 0.15 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.5 | 17.8 | 83.1 | 0 | 0 | 989 | -0.05 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.1 | 16.4 | 79.5 | 0 | 0 | 989 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.4 | 79.2 | 0 | 0 | 989 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.4 | 20.3 | 79.3 | 0 | 0 | 989 | 0.15 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12598 | MCERTS certified instrument
Date downloaded | 2019-07-16 19:23 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2019-06-30
Date of last factory calibration | 2019-06-05
Next service due | 2019-12-05
Date of last Gas Check | 2019-06-05
Security code | [CD9A7ECD]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-07-16 09:21 | 49.1 | 31.6 | 2.5 | 16.8 | 1004 | 169.69 | 1 | 0
BHG010MB | 2019-07-16 09:23 | 48.5 | 32 | 2.4 | 17.1 | 1004 | -6.44 | 1 | 0
BHGV0046 | 2019-07-16 09:28 | 33.1 | 22.9 | 7.9 | 36.1 | 1003 | 0.08 | 0 | 0
BHR0002B | 2019-07-16 09:30 | 33.5 | 20.2 | 1.8 | 44.5 | 1003 | 0.52 | 13 | 0
BHLC002B | 2019-07-16 09:33 | 57.4 | 38.9 | 0.9 | 2.8 | 1003 | 1.75 | 2 | 0
BHLC002B | 2019-07-16 09:33 | 56.9 | 38.8 | 1.5 | 2.8 | 1003 | -0.18 | 1 | 0
BHR0001B | 2019-07-16 09:35 | 58.1 | 33.1 | 1.2 | 7.6 | 1003 | -1.03 | 1 | 0
BHR0001B | 2019-07-16 09:36 | 56.6 | 33.2 | 1.4 | 8.8 | 1003 | -0.06 | 1 | 0
BHR00001 | 2019-07-16 09:37 | 64.9 | 32.1 | 0.8 | 2.2 | 1003 | 1.45 | 1 | 0
BHR00001 | 2019-07-16 09:37 | 63.7 | 32.3 | 0.9 | 3.1 | 1003 | 0.04 | 0 | 0
BHGV0028 | 2019-07-16 09:45 | 4.5 | 3.6 | 15.6 | 76.3 | 1002 | -0.68 | 0 | 0
BHGV0029 | 2019-07-16 09:47 | 56.3 | 35.6 | 1.3 | 6.8 | 1002 | -4.59 | 1 | 0
BHGV000C | 2019-07-16 09:49 | 57.7 | 37.1 | 1.1 | 4.1 | 1002 | -1.43 | 2 | 0
BHR00005 | 2019-07-16 09:52 | 0 | 1.9 | 16.9 | 81.2 | 1002 | 51.24 | 3 | 0
BHLC0005 | 2019-07-16 09:55 | 52.9 | 37.8 | 1.8 | 7.5 | 1002 | 0.16 | 2 | 0
BHLC0005 | 2019-07-16 09:55 | 52.8 | 37.7 | 2 | 7.5 | 1002 | -0.24 | 2 | 0
BHR0006B | 2019-07-16 09:57 | 52 | 38 | 1.9 | 8.1 | 1002 | 2.41 | 2 | 0
BHR0006B | 2019-07-16 09:57 | 51.8 | 38 | 2.3 | 7.9 | 1002 | 0.09 | 1 | 0
BHPW0006 | 2019-07-16 10:00 | 59.9 | 33.7 | 1.4 | 5 | 1002 | 0.3 | 0 | 0
BHPW0006 | 2019-07-16 10:00 | 59.5 | 33.7 | 1.7 | 5.1 | 1002 | 0.13 | 1 | 0
BHGV0049 | 2019-07-16 10:02 | 0.4 | 5.8 | 16.1 | 77.7 | 1002 | -7.27 | 0 | 0
BHGV0049 | 2019-07-16 10:03 | 43.9 | 26.7 | 1.8 | 27.6 | 1002 | -2.31 | 0 | 0
BHG010MB | 2019-07-16 10:06 | 48.9 | 32 | 2.4 | 16.7 | 1002 | -5.15 | 1 | 0
BHG01MDB | 2019-07-16 10:08 | 52.3 | 34 | 1.5 | 12.2 | 1002 | 177.26 | 1 | 0

## August 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-08-09
Weather: | dry
Wind conditions: | calm
Air Temperature: | 14 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.7 | 18.6 | 80.6 | 0 | 0 | 978 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 19.2 | 80.8 | 0 | 0 | 978 | -0.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19.3 | 80.5 | 0 | 0 | 978 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 19.4 | 80.3 | 0 | 0 | 978 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 978 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.7 | 80.1 | 0 | 0 | 978 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.6 | 3.5 | 15.6 | 75.3 | 0 | 0 | 978 | 0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3 | 2 | 16.4 | 78.6 | 0 | 0 | 978 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.4 | 0.8 | 18.4 | 80.4 | 0 | 0 | 978 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0 | 18.2 | 81.7 | 0 | 0 | 978 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 15.7 | 83 | 0 | 0 | 978 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.7 | 18 | 81.3 | 0 | 0 | 978 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 978 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 19 | 80.3 | 0 | 0 | 978 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1 | 16.2 | 82.8 | 0 | 0 | 978 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 18.9 | 81 | 0 | 0 | 978 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 7.1 | 6.6 | 86.3 | 0 | 0 | 978 | -0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.2 | 18.5 | 79.3 | 0 | 0 | 978 | 0.19 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 978 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 16.6 | 81.4 | 0 | 0 | 978 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 18.6 | 81 | 0 | 0 | 978 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.8 | 18.5 | 80.7 | 0 | 0 | 978 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-08-12
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.6 | 19.3 | 80 | 0 | 0 | 997 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0 | 19.2 | 80.7 | 0 | 0 | 997 | -0.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 997 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 997 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 997 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.7 | 80.1 | 0 | 0 | 997 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.4 | 3.3 | 15.9 | 75.4 | 0 | 0 | 997 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.2 | 2.1 | 16.3 | 78.4 | 0 | 0 | 997 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.3 | 0.8 | 18.5 | 80.4 | 0 | 0 | 997 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0 | 18.4 | 81.4 | 0 | 0 | 997 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.2 | 15.6 | 83.2 | 0 | 0 | 997 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.5 | 18.4 | 81.1 | 0 | 0 | 997 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 997 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 997 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 16.4 | 82.5 | 0 | 0 | 997 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 19 | 80.6 | 0 | 0 | 997 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 7 | 9.6 | 83.3 | 0 | 0 | 997 | -0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2 | 18.5 | 79.5 | 0 | 0 | 997 | 0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 997 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.1 | 16.4 | 81.5 | 0 | 0 | 997 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 997 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1 | 18.2 | 80.7 | 0 | 0 | 997 | -0.1 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-08-21
Weather: | dry
Wind conditions: | calm
Air Temperature: | 17 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 18.9 | 80.6 | 0 | 0 | 1007 | 0.18 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 18.9 | 81.1 | 0 | 0 | 1007 | 0.2 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19 | 80.8 | 0 | 0 | 1007 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 19.4 | 80.3 | 0 | 0 | 1007 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 1007 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 19.6 | 80.2 | 0 | 0 | 1007 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.2 | 3.2 | 15.5 | 76.1 | 0 | 0 | 1007 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.4 | 2.1 | 16.2 | 78.3 | 0 | 0 | 1007 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.4 | 0.7 | 18.5 | 80.4 | 0 | 0 | 1007 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0 | 18.1 | 81.8 | 0 | 0 | 1007 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 15.6 | 83.1 | 0 | 0 | 1007 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.5 | 18.6 | 80.9 | 0 | 0 | 1007 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 1007 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 1007 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 0 | 1007 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1007 | 0.12 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.6 | 18.7 | 76.7 | 0 | 0 | 1007 | 0.14 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.1 | 18.4 | 79.5 | 0 | 0 | 1007 | 0.19 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 1007 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 16.5 | 81.1 | 0 | 0 | 1007 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 18.7 | 80.9 | 0 | 0 | 1007 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.2 | 18.7 | 81 | 0 | 0 | 1007 | 0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-08-28
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 996 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.1 | 19.2 | 80.7 | 0 | 0 | 996 | -0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.1 | 80.6 | 0 | 0 | 996 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 996 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 19.4 | 80.2 | 0 | 0 | 996 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 996 | -0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.4 | 3.4 | 15.7 | 75.5 | 0 | 0 | 996 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.9 | 2.4 | 16 | 77.7 | 0 | 0 | 996 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.3 | 0.5 | 18.3 | 80.9 | 0 | 0 | 996 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.1 | 18 | 81.8 | 0 | 0 | 996 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.1 | 15.3 | 83.6 | 0 | 0 | 996 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 996 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 996 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 996 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.4 | 16.6 | 82 | 0 | 0 | 996 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 18.7 | 81.1 | 0 | 0 | 996 | -0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.3 | 14.8 | 82.9 | 0 | 0 | 996 | -0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.2 | 18.6 | 79.2 | 0 | 0 | 996 | 0.21 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  | 100 | 0 | 0 | 996 |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.6 | 17.5 | 81.9 | 0 | 0 | 996 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 16.2 | 81.6 | 0 | 0 | 996 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.3 | 81.2 | 0 | 0 | 996 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.1 | 19.1 | 80.7 | 0 | 0 | 996 | -0.1 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12962 | MCERTS certified instrument
Date downloaded | 2019-08-12 20:24 | Software Version | 1.10.0
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2019-08-09
Date of last factory calibration | 2019-03-25
Next service due | 2019-09-25
Date of last Gas Check | 2019-03-25
Security code | [58D49AEC]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-08-12 09:08 | 42.7 | 34.7 | 0.8 | 21.8 | 998 | 185.85 | 0 | 0
BHG010MB | 2019-08-12 09:33 | 42.3 | 34.5 | 0.9 | 22.3 | 998 | -13.43 | 0 | 0
BHGW0034 | 2019-08-12 09:35 | 0.6 | 4.9 | 14.6 | 79.9 | 998 | -0.29 | 0 | 0
BHGV0017 | 2019-08-12 09:37 | 44.8 | 30.2 | 0.2 | 24.8 | 998 | -11.24 | 0 | 0
BHGV0038 | 2019-08-12 09:38 | 44.3 | 30.4 | 0.5 | 24.8 | 998 | -0.2 | 0 | 0
BHPRG017 | 2019-08-12 09:39 | 44.3 | 30.3 | 1.1 | 24.3 | 998 | -0.19 | 0 | 0
BHGV0037 | 2019-08-12 09:41 | 35.3 | 33.3 | 0.6 | 30.8 | 998 | -1.46 | 0 | 0
BHM010MB | 2019-08-12 09:42 | 54.6 | 41 | 0.1 | 4.3 | 999 | -11.67 | 0 | 0
BHGV0018 | 2019-08-12 09:43 | 54.4 | 41.4 | 0 | 4.2 | 998 | -11.04 | 0 | 0
BHLC004B | 2019-08-12 09:44 | 29.4 | 19.6 | 9.3 | 41.7 | 998 | -0.15 | 3 | 0
BHR0004B | 2019-08-12 09:46 | 51.1 | 40.5 | 0.3 | 8.1 | 998 | -11.34 | 0 | 0
BHGV0015 | 2019-08-12 09:47 | 48.5 | 40.5 | 0.6 | 10.4 | 998 | -11.35 | 0 | 0
BHGV0014 | 2019-08-12 09:49 | 33.2 | 28.2 | 1.2 | 37.4 | 998 | -2.65 | 0 | 0
BHGV0013 | 2019-08-12 09:50 | 22 | 16.6 | 11.6 | 49.8 | 998 | -0.14 | 0 | 0
BHGV0016 | 2019-08-12 09:51 | 61.7 | 39.7 | 0.7 | 0 | 998 | -10.69 | 0 | 0
BHM010MA | 2019-08-12 09:52 | 54.3 | 40.7 | 0.3 | 4.7 | 998 | -11.3 | 0 | 0
BHGV0038 | 2019-08-12 09:53 | 30.3 | 27.1 | 3 | 39.6 | 998 | -7.44 | 0 | 0
BHGV0038 | 2019-08-12 09:53 | 30.5 | 26.7 | 3 | 39.8 | 998 | -0.14 | 0 | 0
BHGV0036 | 2019-08-12 10:04 | 25 | 24 | 1.9 | 49.1 | 998 | -1.11 | 0 | 0
BHGV0035 | 2019-08-12 10:07 | 39 | 40 | 0.2 | 20.8 | 998 | 1.55 | 0 | 0
BHGV0039 | 2019-08-12 10:15 | 33.9 | 24.3 | 4.3 | 37.5 | 998 | 0.56 | 0 | 0
BHPRG039 | 2019-08-12 10:15 | 5.5 | 15.8 | 13.3 | 65.4 | 998 | -0.02 | 0 | 0
BHL000C4 | 2019-08-12 10:20 | 17.2 | 10.7 | 13.7 | 58.4 | 998 | -1.16 | 0 | 0
BHPRL0C4 | 2019-08-12 10:20 | 18 | 11.4 | 13.1 | 57.5 | 998 | 0 | 0 | 0
BHGV0040 | 2019-08-12 10:40 | 37.5 | 30.9 | 0.5 | 31.1 | 999 | -11.48 | 0 | 0
BHGV0040 | 2019-08-12 10:41 | 37.4 | 30.9 | 0.5 | 31.2 | 999 | -0.13 | 0 | 0
BHGV0009 | 2019-08-12 10:42 | 35.8 | 29.7 | 0 | 34.5 | 999 | -12.85 | 0 | 0
BHGV0009 | 2019-08-12 10:42 | 35.9 | 29.8 | 0 | 34.3 | 999 | -0.08 | 0 | 0
BHLC0003 | 2019-08-12 10:48 | 17.6 | 12.6 | 12.9 | 56.9 | 998 | -1.86 | 0 | 0
BHLC0003 | 2019-08-12 10:48 | 17.6 | 12.5 | 12.9 | 57 | 998 | -0.02 | 0 | 0
BHPRL003 | 2019-08-12 10:48 | 17.7 | 12.6 | 12.6 | 57.1 | 998 | -0.02 | 0 | 0
BHGV0301 | 2019-08-12 10:50 | 61.2 | 36.8 | 0.1 | 1.9 | 998 | -12.26 | 0 | 0
BHR00003 | 2019-08-12 10:55 | 24.4 | 16.5 | 11.1 | 48 | 996 | -0.76 | 0 | 0
BHPRR003 | 2019-08-12 10:55 | 23.3 | 14.8 | 11.8 | 50.1 | 997 | -0.04 | 0 | 0
BHGV0046 | 2019-08-12 11:01 | 20.7 | 14.8 | 12.8 | 51.7 | 997 | -3.8 | 0 | 0
BHGV0041 | 2019-08-12 11:04 | 48.6 | 37.6 | 0.2 | 13.6 | 997 | -6.3 | 0 | 0
BHPRG041 | 2019-08-12 11:04 | 48.8 | 37.8 | 0.1 | 13.3 | 997 | -1.7 | 0 | 0
BHPRL006 | 2019-08-12 11:10 | 36.8 | 22.9 | 2.8 | 37.5 | 996 | -0.52 | 4 | 0
BHR0002B | 2019-08-12 11:12 | 34.8 | 21 | 3.5 | 40.7 | 996 | -0.08 | 1 | 0
BHPRR02B | 2019-08-12 11:12 | 35 | 21.1 | 3.5 | 40.4 | 996 | -0.07 | 0 | 0
BHGV0042 | 2019-08-12 11:43 | 37.3 | 23.3 | 4.3 | 35.1 | 998 | -1.76 | 0 | 0
BHGV0042 | 2019-08-12 11:43 | 37.3 | 23.6 | 4.1 | 35 | 998 | -0.2 | 0 | 0
BHPRG042 | 2019-08-12 11:43 | 37.1 | 23.7 | 4.5 | 34.7 | 998 | -0.14 | 0 | 0
BHGV0043 | 2019-08-12 11:47 | 30.7 | 29 | 0.3 | 40 | 998 | -3.49 | 0 | 0
BHGV0043 | 2019-08-12 11:47 | 30.8 | 29 | 0.4 | 39.8 | 998 | -0.13 | 0 | 0
BHGV0007 | 2019-08-12 12:59 | 38.5 | 24.1 | 4.2 | 33.2 | 998 | -1.97 | 0 | 0
BHGV0008 | 2019-08-12 13:02 | 9.7 | 7 | 14.6 | 68.7 | 998 | 0.3 | 9 | 0
BHLC002R | 2019-08-12 13:05 | 0.1 | 1.2 | 18.6 | 80.1 | 998 | -0.06 | 0 | 0
BHGV0044 | 2019-08-12 13:08 | 37.6 | 25.8 | 1.7 | 34.9 | 998 | -1.2 | 0 | 0
BHGV0001 | 2019-08-12 13:12 | 39.7 | 28.8 | 0.4 | 31.1 | 997 | -8.63 | 0 | 0
BHR00001 | 2019-08-12 13:12 | 11.2 | 12.1 | 11.3 | 65.4 | 997 | -14.34 | 0 | 0
BHR00001 | 2019-08-12 13:13 | 11.7 | 11.2 | 11.7 | 65.4 | 997 | -2.69 | 0 | 0
BHGV0045 | 2019-08-12 13:16 | 34.5 | 29.1 | 0.2 | 36.2 | 997 | -11.55 | 0 | 0
BHGV0045 | 2019-08-12 13:17 | 34.2 | 30 | 0.5 | 35.3 | 997 | -0.1 | 0 | 0
BHPRG045 | 2019-08-12 13:17 | 34.2 | 29.9 | 0.9 | 35 | 997 | -0.12 | 0 | 0
BHGV0006 | 2019-08-12 13:23 | 0.1 | 3.6 | 17.7 | 78.6 | 998 | -2.63 | 0 | 0
BHGV0003 | 2019-08-12 13:25 | 68.8 | 32.1 | 0.1 | 0 | 998 | -16.27 | 0 | 0
BHR0001B | 2019-08-12 13:25 | 67.5 | 32.9 | 1.3 | 0 | 998 | -0.1 | 0 | 0
BHR0001B | 2019-08-12 13:26 | 38.5 | 31.2 | 0.3 | 30 | 998 | -16.43 | 0 | 0
BHR0001B | 2019-08-12 13:26 | 38.5 | 31.5 | 0.4 | 29.6 | 998 | -2.32 | 0 | 0
BHR0001B | 2019-08-12 13:28 | 58.8 | 27.5 | 0.6 | 13.1 | 998 | -6.8 | 0 | 0
BHGV0004 | 2019-08-12 13:29 | 58.6 | 27.2 | 0.7 | 13.5 | 998 | -2.56 | 0 | 0
BHLC002B | 2019-08-12 13:41 | 49.8 | 34.7 | 3 | 12.5 | 996 | -5.05 | 0 | 0
BHGV0021 | 2019-08-12 13:42 | 62.8 | 36.4 | 0.2 | 0.6 | 996 | -1.89 | 0 | 0
BHGV0026 | 2019-08-12 13:48 | 50.8 | 36 | 0 | 13.2 | 996 | -13.99 | 0 | 0
BHGV0027 | 2019-08-12 13:58 | 45.8 | 35.8 | 0.1 | 18.3 | 996 | -13.62 | 0 | 0
BHGV0047 | 2019-08-12 14:06 | 25.4 | 15.4 | 6.9 | 52.3 | 997 | 0.96 | 4 | 0
BHGV000C | 2019-08-12 14:17 | 61.4 | 38.1 | 0.1 | 0.4 | 996 | -8.23 | 0 | 0
BHGV0029 | 2019-08-12 14:18 | 55.5 | 38.8 | 0 | 5.7 | 996 | -15.17 | 0 | 0
BHLC0005 | 2019-08-12 14:23 | 58 | 43.1 | 0 | 0 | 996 | 0.29 | 0 | 0
BHLC0005 | 2019-08-12 14:24 | 57.5 | 43.1 | 0.1 | 0 | 996 | -1.97 | 0 | 0
BHLC006B | 2019-08-12 14:35 | 60.5 | 39.4 | 0.3 | 0 | 996 | 2.67 | 0 | 0
BHLC006B | 2019-08-12 14:35 | 60.9 | 39.9 | 0.3 | 0 | 996 | -0.79 | 0 | 0
BHGV0049 | 2019-08-12 14:36 | 59.9 | 37.6 | 0.5 | 2 | 997 | -0.57 | 0 | 0
BHGV0049 | 2019-08-12 14:37 | 59.4 | 39.7 | 0.6 | 0.3 | 997 | -2.47 | 0 | 0
BHPRG049 | 2019-08-12 14:37 | 59.2 | 39.6 | 0.7 | 0.5 | 997 | -1.83 | 0 | 0
BHG010MA | 2019-08-12 14:39 | 46.5 | 36.6 | 0.7 | 16.2 | 997 | -15.98 | 0 | 0
BHG01MDA | 2019-08-12 14:41 | 47.2 | 35.9 | 0.6 | 16.3 | 997 | 183.56 | 0 | 0

## September 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-09-02
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.7 | 18.5 | 80.8 | 0 | 0 | 1006 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0 | 19.2 | 80.7 | 0 | 0 | 1006 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 1006 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.4 | 19.7 | 79.9 | 0 | 0 | 1006 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 1006 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.9 | 80.9 | 0 | 0 | 1006 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.5 | 3.1 | 15.6 | 75.8 | 0 | 0 | 1006 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.6 | 2.4 | 16.2 | 77.8 | 0 | 0 | 1006 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 0.2 | 18.2 | 81.4 | 0 | 0 | 1006 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.3 | 18.4 | 81.1 | 0 | 0 | 1006 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.2 | 18.4 | 80.4 | 0 | 0 | 1006 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.5 | 18.8 | 80.7 | 0 | 0 | 1006 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 1006 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1006 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 1006 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 19 | 80.8 | 0 | 0 | 1006 | -0.16 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 3.4 | 13.4 | 83.1 | 0 | 0 | 1006 | -0.63 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.3 | 18.9 | 78.8 | 0 | 0 | 1006 | 0.19 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.5 | 17.6 | 81.9 | 0 | 0 | 1006 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 16.9 | 80.7 | 0 | 0 | 1006 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 18.5 | 81.1 | 0 | 0 | 1006 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.1 | 19 | 80.8 | 0 | 0 | 1006 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-09-11
Weather: | dry
Wind conditions: | calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.1 | 16.7 | 82.2 | 0 | 0 | 998 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 18.8 | 80.9 | 0 | 0 | 998 | -0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.4 | 80.3 | 0 | 0 | 998 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 998 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 19.5 | 80.3 | 0 | 0 | 998 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 18.5 | 81.2 | 0 | 0 | 998 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.1 | 3.2 | 15.9 | 75.8 | 0 | 0 | 998 | 0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.4 | 2.5 | 15.9 | 78.2 | 0 | 0 | 998 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.4 | 0.3 | 18.6 | 80.7 | 0 | 0 | 998 | -0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0.3 | 18.5 | 80.9 | 0 | 0 | 998 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.9 | 18.6 | 80.5 | 0 | 0 | 998 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.9 | 80.7 | 0 | 0 | 998 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 998 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19.1 | 80.5 | 0 | 0 | 998 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.1 | 16.5 | 82.4 | 0 | 0 | 998 | -0.01 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 18.5 | 81.3 | 0 | 0 | 998 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.3 | 12.6 | 85.1 | 0 | 0 | 998 | -0.13 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.6 | 18.8 | 78.6 | 0 | 0 | 998 | 0.17 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  | 100 |  |  |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 998 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 16.5 | 81 | 0 | 0 | 998 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 998 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 17.8 | 81.7 | 0 | 0 | 998 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-09-20
Weather: | dry
Wind conditions: | calm
Air Temperature: | 12 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1 | 17.3 | 82.2 | 0 | 0 | 1013 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 1013 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19.5 | 80.3 | 0 | 0 | 1013 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1013 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 1013 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.6 | 81.2 | 0 | 0 | 1013 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5 | 3.5 | 16.2 | 75.3 | 0 | 0 | 1013 | 0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.6 | 2.1 | 16.2 | 78.1 | 0 | 0 | 1013 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.5 | 0.4 | 18.5 | 80.6 | 0 | 0 | 1013 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.2 | 18.6 | 81 | 0 | 0 | 1013 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 18.5 | 80.7 | 0 | 0 | 1013 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1013 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 1013 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1013 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 16.8 | 82 | 0 | 0 | 1013 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 1013 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.8 | 13.3 | 84.9 | 0 | 0 | 1013 | -0.05 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.4 | 18.7 | 78.9 | 0 | 0 | 1013 | 0.16 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.5 | 17.5 | 82 | 0 | 0 | 1013 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 16.4 | 81.2 | 0 | 0 | 1013 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 18.5 | 80.8 | 0 | 0 | 1013 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.3 | 18.1 | 81.6 | 0 | 0 | 1013 | -0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## October 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-10-03
Weather: | dry
Wind conditions: | calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 17.7 | 81.1 | 0 | 0 | 1001 | -0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 19.1 | 80.6 | 0 | 0 | 1001 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 1001 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 1001 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 19.1 | 80.6 | 0 | 0 | 1001 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.8 | 81 | 0 | 0 | 1001 | -0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.9 | 3 | 16.5 | 75.6 | 0 | 0 | 1001 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.7 | 2.2 | 16.6 | 77.5 | 0 | 0 | 1001 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.6 | 0.5 | 18.3 | 80.6 | 0 | 0 | 1001 | -0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0.4 | 18.1 | 81.2 | 0 | 0 | 1001 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.6 | 18.2 | 81.2 | 0 | 0 | 1001 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 19 | 80.7 | 0 | 0 | 1001 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 1001 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 19 | 80.6 | 0 | 0 | 1001 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.4 | 17.1 | 81.5 | 0 | 0 | 1001 | -0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 19.5 | 80.4 | 0 | 0 | 1001 | -0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2 | 13.9 | 84.1 | 0 | 0 | 1001 | -0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.3 | 18.6 | 79.1 | 0 | 0 | 1001 | 0.14 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.5 | 17.5 | 82 | 0 | 0 | 1001 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 16.4 | 81.2 | 0 | 0 | 1001 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 18.5 | 80.8 | 0 | 0 | 1001 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1001 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-10-10
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 |  | 0 | 1.4 | 17.5 | 81.1 | 0 | 0 | 987 | -0.08 | 1 | 8.8
BK BH 3 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 987 | -0.01 | 1 | 3.1
BK BH 4 |  | 0 | 0.4 | 19.6 | 80 | 0 | 0 | 987 | -0.03 | 1 | 5.1
BK BH 5 |  | 0 | 0.3 | 19.4 | 80.3 | 0 | 0 | 987 | -0.04 | 1 | 1.5
BK BH 6 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 987 | 0.01 | 1 | 1.5
BK BH 7 |  | 0 | 0.3 | 19 | 80.7 | 0 | 0 | 987 | -0.09 | 1 | 10
BK BH 8 |  | 4.5 | 2.8 | 16.7 | 76 | 0 | 0 | 987 | 0.01 | 32.2 | 3.6
BK BH 9 |  | 3.2 | 2.3 | 16.8 | 77.7 | 0 | 0 | 987 | 0 | 29.6 | 10.4
BK BH 10 |  | 0.5 | 0.6 | 18.2 | 80.7 | 0 | 0 | 987 | -0.05 | 1 | 3.9
BK BH 11 |  | 0.2 | 0.5 | 18.4 | 80.9 | 0 | 0 | 987 | 0 | 1 | 6.5
BK BH 12 |  | 0 | 0.5 | 18.1 | 81.4 | 0 | 0 | 987 | -0.05 | 1 | 6.6
BK BH 13 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 987 | 0.01 | 1 | 9.4
BK BH 14 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 987 | -0.02 | 1 | 3.5
BK BH 15 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 987 | -0.04 | 1 | 17.6
BK BH 16 |  | 0 | 1.6 | 17.4 | 81 | 0 | 0 | 987 | -0.02 | 1 | 11.4
BK BH 17 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 987 | -0.04 | 1 | 12.9
BK BH 18 |  | 0 | 2.1 | 15.2 | 82.7 | 0 | 0 | 987 | -0.05 | 6.8 | 21.2
BK BH 19 |  | 0 | 2.2 | 18.7 | 79.1 | 0 | 0 | 987 | 0.11 | 1 | 11.2
BK BH 20 | Buried | [8 empty] | 1 | 10.7
BK BH 21 |  | 0 | 0.4 | 17.4 | 82.2 | 0 | 0 | 987 | -0.02 | 1 | 21.7
BK BH 23 |  | 0 | 2.2 | 16.8 | 81 | 0 | 0 | 987 | 0.02 | 1 | 7.3
BK BH 24 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 987 | 0.01 | 1 | 1.5
BK BH 25 |  | 0 | 0.3 | 18.5 | 81.2 | 0 | 0 | 987 | -0.02 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-10-16
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 |  | 0 | 1.1 | 17.6 | 81.3 | 0 | 0 | 985 | -0.05 | 1 | 8.8
BK BH 3 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 985 | -0.03 | 1 | 3.1
BK BH 4 |  | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 985 | -0.03 | 1 | 5.1
BK BH 5 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 985 | -0.04 | 1 | 1.5
BK BH 6 |  | 0 | 0.3 | 19.8 | 79.9 | 0 | 0 | 985 | 0.01 | 1 | 1.5
BK BH 7 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 985 | -0.08 | 1 | 10
BK BH 8 |  | 5 | 2.5 | 16.8 | 75.7 | 0 | 0 | 985 | 0.01 | 32.2 | 3.6
BK BH 9 |  | 3.4 | 2.1 | 16.9 | 77.6 | 0 | 0 | 985 | 0 | 29.6 | 10.4
BK BH 10 |  | 0.4 | 0.8 | 18 | 80.8 | 0 | 0 | 985 | -0.04 | 1 | 3.9
BK BH 11 |  | 0.4 | 0.6 | 18.2 | 80.8 | 0 | 0 | 985 | 0 | 1 | 6.5
BK BH 12 |  | 0 | 0.4 | 18.4 | 81.2 | 0 | 0 | 985 | -0.05 | 1 | 6.6
BK BH 13 |  | 0 | 0.5 | 19 | 80.5 | 0 | 0 | 985 | -0.01 | 1 | 9.4
BK BH 14 |  | 0 | 0.3 | 17.8 | 81.9 | 0 | 0 | 985 | -0.03 | 1 | 3.5
BK BH 15 |  | 0 | 0.5 | 19.1 | 80.4 | 0 | 0 | 985 | -0.05 | 1 | 17.6
BK BH 16 |  | 0 | 1.4 | 17.6 | 81 | 0 | 0 | 985 | -0.01 | 1 | 11.4
BK BH 17 |  | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 985 | -0.04 | 1 | 12.9
BK BH 18 |  | 0 | 2.5 | 15.4 | 82.1 | 0 | 0 | 985 | -0.02 | 6.8 | 21.2
BK BH 19 |  | 0 | 2.3 | 18.5 | 79.2 | 0 | 0 | 985 | 0.08 | 1 | 11.2
BK BH 20 | Buried | [8 empty] | 1 | 10.7
BK BH 21 |  | 0 | 0.5 | 17.6 | 81.9 | 0 | 0 | 985 | -0.03 | 1 | 21.7
BK BH 23 |  | 0 | 2.1 | 16.9 | 81 | 0 | 0 | 985 | 0.01 | 1 | 7.3
BK BH 24 |  | 0 | 0.5 | 18.3 | 81.2 | 0 | 0 | 985 | 0.01 | 1 | 1.5
BK BH 25 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 985 | -0.01 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-10-23
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 |  | 0 | 1.2 | 17.5 | 81.3 | 0 | 0 | 1005 | -0.04 | 1 | 8.8
BK BH 3 |  | 0 | 0.4 | 19 | 80.6 | 0 | 0 | 1005 | -0.02 | 1 | 3.1
BK BH 4 |  | 0 | 0.5 | 19.3 | 80.2 | 0 | 0 | 1005 | -0.03 | 1 | 5.1
BK BH 5 |  | 0 | 0.3 | 19.5 | 80.2 | 0 | 0 | 1005 | -0.04 | 1 | 1.5
BK BH 6 |  | 0 | 0.4 | 19.9 | 79.7 | 0 | 0 | 1005 | 0.04 | 1 | 1.5
BK BH 7 |  | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1005 | -0.06 | 1 | 10
BK BH 8 |  | 4.8 | 2.4 | 16.9 | 75.9 | 0 | 0 | 1005 | 0.01 | 32.2 | 3.6
BK BH 9 |  | 3.8 | 2.3 | 17 | 76.9 | 0 | 0 | 1005 | 0 | 29.6 | 10.4
BK BH 10 |  | 0.3 | 0.7 | 18.2 | 80.8 | 0 | 0 | 1005 | -0.03 | 1 | 3.9
BK BH 11 |  | 0.2 | 0.7 | 18.5 | 80.6 | 0 | 0 | 1005 | 0 | 1 | 6.5
BK BH 12 |  | 0 | 0.5 | 18.9 | 80.6 | 0 | 0 | 1005 | -0.05 | 1 | 6.6
BK BH 13 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 1005 | -0.02 | 1 | 9.4
BK BH 14 |  | 0 | 0.4 | 18 | 81.6 | 0 | 0 | 1005 | -0.02 | 1 | 3.5
BK BH 15 |  | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1005 | -0.05 | 1 | 17.6
BK BH 16 |  | 0 | 1.3 | 17.8 | 80.9 | 0 | 0 | 1005 | -0.01 | 1 | 11.4
BK BH 17 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1005 | -0.05 | 1 | 12.9
BK BH 18 |  | 0 | 2.6 | 15.9 | 81.5 | 0 | 0 | 1005 | -0.02 | 6.8 | 21.2
BK BH 19 |  | 0 | 2.2 | 18 | 79.8 | 0 | 0 | 1005 | 0.06 | 1 | 11.2
BK BH 20 | Buried | [8 empty] | 1 | 10.7
BK BH 21 |  | 0 | 0.4 | 17.8 | 81.8 | 0 | 0 | 1005 | -0.02 | 1 | 21.7
BK BH 23 |  | 0 | 2 | 16.5 | 81.5 | 0 | 0 | 1005 | 0.01 | 1 | 7.3
BK BH 24 |  | 0 | 0.4 | 18.1 | 81.5 | 0 | 0 | 1005 | 0.02 | 1 | 1.5
BK BH 25 |  | 0 | 0.3 | 18.9 | 80.8 | 0 | 0 | 1005 | -0.01 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-10-29
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 %
BK BH 1 |  | 0 | 1.1 | 17.4 | 81.5 | 0 | 0 | 1020 | -0.02 | 1 | 8.8
BK BH 3 |  | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 1020 | -0.03 | 1 | 3.1
BK BH 4 |  | 0 | 0.4 | 19.5 | 80.1 | 0 | 0 | 1020 | -0.03 | 1 | 5.1
BK BH 5 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 1020 | -0.03 | 1 | 1.5
BK BH 6 |  | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 1020 | 0.04 | 1 | 1.5
BK BH 7 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1020 | -0.04 | 1 | 10
BK BH 8 |  | 5.4 | 2.2 | 16.5 | 75.9 | 0 | 0 | 1020 | 0.01 | 32.2 | 3.6
BK BH 9 |  | 3.5 | 2.1 | 17.4 | 77 | 0 | 0 | 1020 | 0 | 29.6 | 10.4
BK BH 10 |  | 0.4 | 0.5 | 18.3 | 80.8 | 0 | 0 | 1020 | -0.03 | 1 | 3.9
BK BH 11 |  | 0.3 | 0.8 | 18.4 | 80.5 | 0 | 0 | 1020 | 0 | 1 | 6.5
BK BH 12 |  | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 1020 | -0.03 | 1 | 6.6
BK BH 13 |  | 0 | 0.7 | 18.5 | 80.8 | 0 | 0 | 1020 | -0.02 | 1 | 9.4
BK BH 14 |  | 0 | 0.5 | 18.5 | 81 | 0 | 0 | 1020 | -0.02 | 1 | 3.5
BK BH 15 |  | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 1020 | -0.04 | 1 | 17.6
BK BH 16 |  | 0 | 1.2 | 17.5 | 81.3 | 0 | 0 | 1020 | -0.01 | 1 | 11.4
BK BH 17 |  | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1020 | -0.02 | 1 | 12.9
BK BH 18 |  | 0 | 2.4 | 16 | 81.6 | 0 | 0 | 1020 | -0.04 | 6.8 | 21.2
BK BH 19 |  | 0 | 2.3 | 18.4 | 79.3 | 0 | 0 | 1020 | 0.04 | 1 | 11.2
BK BH 20 | Buried | [8 empty] | 1 | 10.7
BK BH 21 |  | 0 | 0.6 | 17.5 | 81.9 | 0 | 0 | 1020 | -0.03 | 1 | 21.7
BK BH 23 |  | 0 | 2.1 | 16.4 | 81.5 | 0 | 0 | 1020 | 0.05 | 1 | 7.3
BK BH 24 |  | 0 | 0.5 | 18.2 | 81.3 | 0 | 0 | 1020 | 0.04 | 1 | 1.5
BK BH 25 |  | 0 | 0.4 | 19 | 80.6 | 0 | 0 | 1020 | -0.03 | 1 | 9.9
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12598 | MCERTS certified instrument
Date downloaded | 2019-10-16 12:39 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2019-10-07
Date of last factory calibration | 2019-06-05
Next service due | 2019-12-05
Date of last Gas Check | 2019-06-05
Security code | [45897997]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-10-16 09:43 | 53.3 | 35.3 | 1.4 | 10 | 985 | 185.81 | 0 | 0
BHG01MDB | 2019-10-16 09:44 | 52.5 | 36.1 | 0.7 | 10.7 | 985 | 21.13 | 2 | 0
BHGV0037 | 2019-10-16 09:54 | 69.3 | 32.8 | 0.8 | 0 | 985 | 0.69 | 0 | 0
BHGV0037 | 2019-10-16 09:55 | 68.3 | 33.6 | 0.3 | 0 | 985 | -1.34 | 0 | 0
BHM010MB | 2019-10-16 09:56 | 60.4 | 39.3 | 0.3 | 0 | 985 | -10.31 | 3 | 0
BHGV0018 | 2019-10-16 09:59 | 58.5 | 41.7 | 0.5 | 0 | 985 | -10.66 | 2 | 0
BHLC004B | 2019-10-16 10:03 | 12.5 | 10.8 | 12.5 | 64.2 | 985 | -0.06 | 7 | 0
BHR0004B | 2019-10-16 10:05 | 1.1 | 16.4 | 9 | 73.5 | 985 | 53.35 | 10 | 0
BHGV0015 | 2019-10-16 10:10 | 57.4 | 40.8 | 1.5 | 0.3 | 985 | -10.41 | 1 | 0
BHGV0014 | 2019-10-16 10:11 | 62.2 | 38.3 | 0.5 | 0 | 985 | -1.36 | 3 | 0
BHGV0014 | 2019-10-16 10:11 | 62 | 38.6 | 0.4 | 0 | 985 | -10.44 | 3 | 0
BHGV0013 | 2019-10-16 10:13 | 0.2 | 4.9 | 14.3 | 80.6 | 985 | -1.59 | 0 | 0
BHGV0016 | 2019-10-16 10:15 | 64 | 34.6 | 0.6 | 0.8 | 985 | -10.38 | 1 | 0
BHM010MA | 2019-10-16 10:17 | 61.5 | 38.4 | 0.7 | 0 | 985 | -10.34 | 2 | 0
BHL000C4 | 2019-10-16 10:19 | 48.8 | 23.3 | 10.2 | 17.7 | 985 | 0.16 | 0 | 0
BHGV0017 | 2019-10-16 10:20 | 30.5 | 33.4 | 3.9 | 32.2 | 985 | -0.2 | 1 | 0
BHGV0038 | 2019-10-16 10:22 | 65.8 | 33.8 | 0.2 | 0.2 | 984 | -1.21 | 1 | 0
BHGV0038 | 2019-10-16 10:22 | 65.6 | 34 | 0.3 | 0.1 | 984 | -1.03 | 1 | 0
BHGV0039 | 2019-10-16 10:24 | 69.1 | 33.1 | 0.4 | 0 | 985 | 2.18 | 1 | 0
BHGV0039 | 2019-10-16 10:24 | 67.7 | 33 | 0.2 | 0 | 985 | -0.08 | 1 | 0
BHGV0010 | 2019-10-16 10:28 | 45.1 | 28.5 | 0.1 | 26.3 | 985 | -0.48 | 0 | 0
BHGV0040 | 2019-10-16 10:30 | 38.3 | 31.8 | 0.6 | 29.3 | 985 | -6 | 0 | 0
BHGV0040 | 2019-10-16 10:30 | 38.3 | 32.1 | 0.5 | 29.1 | 985 | -2.03 | 0 | 0
BHLC001B | 2019-10-16 10:32 | 65.2 | 36.3 | 0.6 | 0 | 985 | 0.45 | 1 | 0
BHLC001B | 2019-10-16 10:32 | 65.2 | 36.5 | 0.2 | 0 | 985 | -0.28 | 1 | 0
BHGV0009 | 2019-10-16 10:33 | 66.2 | 34.6 | 0.7 | 0 | 985 | 1.64 | 1 | 0
BHGV0009 | 2019-10-16 10:33 | 66.2 | 35.1 | 0.3 | 0 | 985 | 0.11 | 1 | 0
BHGV0041 | 2019-10-16 10:36 | 61.6 | 39.6 | 0.5 | 0 | 985 | -1.56 | 2 | 0
BHGV0041 | 2019-10-16 10:36 | 60.8 | 39.9 | 0.2 | 0 | 985 | -0.49 | 3 | 0
BHGV0046 | 2019-10-16 10:38 | 0.1 | 1.7 | 16.6 | 81.6 | 984 | -2.28 | 0 | 0
BHR0002B | 2019-10-16 10:39 | 10.8 | 12.2 | 1.5 | 75.5 | 984 | 0.39 | 20 | 0
BHGV0026 | 2019-10-16 10:43 | 55.3 | 37 | 0.8 | 6.9 | 984 | -8.14 | 1 | 0
BHR0002B | 2019-10-16 10:45 | 47.7 | 31.9 | 3.6 | 16.8 | 984 | -3.47 | 1 | 0
BHGV0045 | 2019-10-16 10:48 | 60 | 34.2 | 0.2 | 5.6 | 984 | -4.27 | 1 | 0
BHGV0045 | 2019-10-16 10:48 | 59.3 | 34.4 | 0.1 | 6.2 | 984 | -6.53 | 1 | 0
BHR0001B | 2019-10-16 10:50 | 65.1 | 37.3 | 0.1 | 0 | 984 | 0.48 | 0 | 0
BHR0001B | 2019-10-16 10:50 | 64.7 | 37.4 | 0.4 | 0 | 984 | -0.38 | 0 | 0
BHR00001 | 2019-10-16 10:52 | 47.2 | 28.5 | 3.7 | 20.6 | 984 | 1.88 | 0 | 0
BHGV0006 | 2019-10-16 10:53 | 65.1 | 35.8 | 0.6 | 0 | 984 | -2.55 | 0 | 0
BHGV0043 | 2019-10-16 10:56 | 50.1 | 28.9 | 1.5 | 19.5 | 985 | -19.42 | 0 | 0
BHGV0007 | 2019-10-16 10:59 | 59.4 | 32.1 | 0.5 | 8 | 985 | -7.63 | 0 | 0
BHGV0007 | 2019-10-16 10:59 | 59.4 | 31.7 | 0.4 | 8.5 | 985 | 0.17 | 0 | 0
BHGV0008 | 2019-10-16 11:00 | 7.8 | 9.5 | 11.5 | 71.2 | 985 | 4.02 | 4 | 0
BHLC002R | 2019-10-16 11:01 | 1.4 | 3.2 | 15.8 | 79.6 | 985 | -2.42 | 2 | 0
BHGV0044 | 2019-10-16 11:03 | 59.7 | 30.2 | 1.1 | 9 | 985 | -8.46 | 0 | 0
BHGV0004 | 2019-10-16 11:06 | 74.2 | 26.7 | 1.3 | 0 | 985 | -0.01 | 0 | 0
BHGV0004 | 2019-10-16 11:06 | 73.8 | 27.9 | 0.7 | 0 | 985 | -0.2 | 0 | 0
BHGV0003 | 2019-10-16 11:08 | 69.1 | 33.9 | 0.1 | 0 | 986 | -8.33 | 0 | 0
BHGV0006 | 2019-10-16 11:10 | 66 | 36.7 | 0.1 | 0 | 986 | -2.06 | 0 | 0
BHGV0006 | 2019-10-16 11:10 | 65 | 36.8 | 0.4 | 0 | 986 | -0.78 | 0 | 0
BHGV0045 | 2019-10-16 11:13 | 59.4 | 34.5 | 0.1 | 6 | 986 | -7.79 | 0 | 0
BHGV0027 | 2019-10-16 11:19 | 57.4 | 37.8 | 0.5 | 4.3 | 984 | -7.89 | 0 | 0
BHGV0028 | 2019-10-16 11:21 | 0.1 | 1.8 | 16.7 | 81.4 | 984 | -2.65 | 0 | 0
BHGV0029 | 2019-10-16 11:23 | 58.4 | 38.3 | 0.2 | 3.1 | 984 | -7.76 | 1 | 0
BHGV000C | 2019-10-16 11:25 | 59.7 | 40.8 | 0.2 | 0 | 984 | -5.05 | 3 | 2
BHR00005 | 2019-10-16 11:28 | 0.1 | 3.1 | 16.4 | 80.4 | 984 | 107.88 | 0 | 0
BHGV0031 | 2019-10-16 11:30 | 63.3 | 37.8 | 0.5 | 0 | 984 | -7.47 | 0 | 0
BHGV0031 | 2019-10-16 11:30 | 62.3 | 38.6 | 0.4 | 0 | 984 | -1.79 | 0 | 0
BHLC0005 | 2019-10-16 11:33 | 56.2 | 40.4 | 1.1 | 2.3 | 984 | 0.08 | 2 | 0
BHLC0005 | 2019-10-16 11:33 | 53.7 | 39.9 | 1.7 | 4.7 | 984 | -0.84 | 1 | 0
BHR0006B | 2019-10-16 11:34 | 57.6 | 40.7 | 0.8 | 0.9 | 984 | 2.31 | 2 | 0
BHR0006B | 2019-10-16 11:35 | 57.7 | 40.9 | 0.6 | 0.8 | 984 | -1.73 | 2 | 0
BHLC0006 | 2019-10-16 11:38 | 65.6 | 37.5 | 0.4 | 0 | 985 | -1.36 | 0 | 0
BHLC0006 | 2019-10-16 11:38 | 63.1 | 37.9 | 0.4 | 0 | 985 | -1.41 | 0 | 0
BHGV0033 | 2019-10-16 11:40 | 53.1 | 34.4 | 1.4 | 11.1 | 984 | -5.05 | 0 | 0
BHGV0049 | 2019-10-16 11:42 | 43.3 | 28.5 | 0.7 | 27.5 | 985 | -3.71 | 0 | 0
BHGV0049 | 2019-10-16 11:42 | 43.2 | 28.6 | 0.6 | 27.6 | 985 | -1.39 | 0 | 0
BHGW0034 | 2019-10-16 11:44 | 18.8 | 10.9 | 8.7 | 61.6 | 985 | 0.22 | 0 | 0
BHG010MB | 2019-10-16 11:47 | 54.5 | 35.6 | 0.8 | 9.1 | 985 | -9.68 | 1 | 0
BHG01MDB | 2019-10-16 11:50 | 54.3 | 35.9 | 0.8 | 9 | 985 | 186.68 | 1 | 0

## November 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-11-06
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 7 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50%
992
BK BH 1 |  | 0 | 1.4 | 17 | 81.6 | 0 | 0 | 992 | -0.03 | 1 | 8.8 | 0.5
BK BH 3 |  | 0 | 0.9 | 19.5 | 79.6 | 0 | 0 | 992 | -0.05 | 1 | 3.1 | 0.5
BK BH 4 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 992 | -0.04 | 1 | 5.1 | 0.5
BK BH 5 |  | 0 | 0.4 | 19.3 | 80.3 | 0 | 0 | 992 | -0.02 | 1 | 1.5 | 0.5
BK BH 6 |  | 0 | 0.4 | 20.1 | 79.5 | 0 | 0 | 992 | 0.01 | 1 | 1.5 | 0.5
BK BH 7 |  | 0 | 0.6 | 19.6 | 79.8 | 0 | 0 | 992 | -0.06 | 1 | 10 | 0.5
BK BH 8 |  | 5.2 | 2.4 | 16.8 | 75.6 | 0 | 0 | 992 | 0 | 32.2 | 3.6 | 16.1
BK BH 9 |  | 3.6 | 2.1 | 17.6 | 76.7 | 0 | 0 | 992 | 0 | 29.6 | 10.4 | 14.8
BK BH 10 |  | 0.5 | 0.4 | 18.5 | 80.6 | 0 | 0 | 992 | 0 | 1 | 3.9 | 0.5
BK BH 11 |  | 0.4 | 0.8 | 18.6 | 80.2 | 0 | 0 | 992 | 0.01 | 1 | 6.5 | 0.5
BK BH 12 |  | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 992 | -0.02 | 1 | 6.6 | 0.5
BK BH 13 |  | 0 | 0.5 | 18.6 | 80.9 | 0 | 0 | 992 | -0.04 | 1 | 9.4 | 0.5
BK BH 14 |  | 0 | 0.6 | 18.6 | 80.8 | 0 | 0 | 992 | -0.06 | 1 | 3.5 | 0.5
BK BH 15 |  | 0 | 0.5 | 19.4 | 80.1 | 0 | 0 | 992 | -0.01 | 1 | 17.6 | 0.5
BK BH 16 |  | 0 | 1.3 | 17.6 | 81.1 | 0 | 0 | 992 | 0 | 1 | 11.4 | 0.5
BK BH 17 |  | 0 | 0.4 | 19.4 | 80.2 | 0 | 0 | 992 | -0.03 | 1 | 12.9 | 0.5
BK BH 18 |  | 0 | 2.5 | 16.3 | 81.2 | 0 | 0 | 992 | -0.05 | 6.8 | 21.2 | 3.4
BK BH 19 |  | 0 | 2.2 | 18.5 | 79.3 | 0 | 0 | 992 | 0.02 | 1 | 11.2 | 0.5
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5
BK BH 21 |  | 0 | 0.7 | 17.6 | 81.7 | 0 | 0 | 992 | -0.02 | 1 | 21.7 | 0.5
BK BH 23 |  | 0 | 2.2 | 16.8 | 81 | 0 | 0 | 992 | 0.04 | 1 | 7.3 | 0.5
BK BH 24 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 992 | 0.03 | 1 | 1.5 | 0.5
BK BH 25 |  | 0 | 0.5 | 19.3 | 80.2 | 0 | 0 | 992 | -0.01 | 1 | 9.9 | 0.5
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-11-12
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 17.5 | 81.3 | 0 | 0 | 980 | -0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 980 | -0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.8 | 19.6 | 79.6 | 0 | 0 | 980 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.6 | 19.5 | 79.9 | 0 | 0 | 980 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 20 | 79.5 | 0 | 0 | 980 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 980 | -0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.9 | 2.3 | 17.2 | 75.6 | 0 | 0 | 980 | 0 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.5 | 2.2 | 17.4 | 76.9 | 0 | 0 | 980 | 0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.6 | 0.7 | 18.9 | 79.8 | 0 | 0 | 980 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.5 | 0.5 | 18.9 | 80.1 | 0 | 0 | 980 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 19.4 | 79.8 | 0 | 0 | 980 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 980 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.8 | 18.9 | 80.3 | 0 | 0 | 980 | -0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 980 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.2 | 17.9 | 80.9 | 0 | 0 | 980 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.6 | 19.2 | 80.2 | 0 | 0 | 980 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.4 | 16.8 | 80.8 | 0 | 0 | 980 | -0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.5 | 18.9 | 78.6 | 0 | 0 | 980 | 0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.6 | 17.8 | 81.6 | 0 | 0 | 980 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.1 | 17 | 80.9 | 0 | 0 | 980 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 18.6 | 80.7 | 0 | 0 | 980 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 980 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-11-21
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12962
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.3 | 17.4 | 81.3 | 0 | 0 | 990 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 990 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 990 | -0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 990 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 990 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 990 | 0 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.2 | 2.5 | 17.9 | 74.4 | 0 | 0 | 990 | -0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.6 | 2.1 | 17.8 | 76.5 | 0 | 0 | 990 | 0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.7 | 0.9 | 19 | 79.4 | 0 | 0 | 990 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.4 | 0.6 | 18.5 | 80.5 | 0 | 0 | 990 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.9 | 19.3 | 79.8 | 0 | 0 | 990 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.7 | 18.5 | 80.8 | 0 | 0 | 990 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 18.4 | 80.7 | 0 | 0 | 990 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.8 | 19.1 | 80.1 | 0 | 0 | 990 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.6 | 18.2 | 80.2 | 0 | 0 | 990 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.9 | 19.1 | 80 | 0 | 0 | 990 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.4 | 17 | 80.6 | 0 | 0 | 990 | -0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.9 | 18.5 | 78.6 | 0 | 0 | 990 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 990 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 17.6 | 79.9 | 0 | 0 | 990 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 990 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 990 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-11-27
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 18 | 81.8 | 0 | 0 | 965 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.3 | 12.3 | 85.3 | 0 | 0 | 966 | 0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 966 | -0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 966 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 966 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 966 | 0 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.5 | 1.9 | 13.3 | 80.3 | 0 | 0 | 965 | 0.36 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.4 | 5 | 15.7 | 70.9 | 0 | 0 | 965 | 0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.7 | 0.9 | 19 | 79.4 | 0 | 0 | 965 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.4 | 0.6 | 18.5 | 80.5 | 0 | 0 | 965 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 6.2 | 5.2 | 88.5 | 0 | 0 | 966 | 0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.6 | 18.4 | 81 | 0 | 0 | 965 | -0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 18.3 | 81.6 | 0 | 0 | 965 | -0.16 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.3 | 17.9 | 81.7 | 0 | 0 | 965 | 0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 0.1 | 12.9 | 86.8 | 0 | 0 | 965 | 0.25 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0 | 17.6 | 82.3 | 0 | 0 | 964 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.3 | 7.9 | 2.2 | 89.6 | 0 | 0 | 964 | 0 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.6 | 18.4 | 79 | 0 | 0 | 965 | 0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.9 | 12.8 | 84.2 | 0 | 0 | 964 | 0.59 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 6.7 | 11.6 | 81.7 | 0 | 0 | 965 | -0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 18.1 | 81.8 | 0 | 0 | 965 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.4 | 17.4 | 81.2 | 0 | 0 | 965 | 0.37 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12598 | MCERTS certified instrument
Date downloaded | 2019-11-12 11:47 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2019-10-07
Date of last factory calibration | 2019-06-05
Next service due | 2019-12-05
Date of last Gas Check | 2019-06-05
Security code | [6D56A963]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2019-11-12 09:22 | 50 | 34.8 | 1.5 | 13.7 | 981 | 174.37 | 0 | 0
BHG010MB | 2019-11-12 09:25 | 48.6 | 34.3 | 1.8 | 15.3 | 981 | -28.31 | 0 | 0
BHGV0035 | 2019-11-12 09:28 | 61.6 | 41.8 | 0.1 | 0 | 980 | -2.99 | 1 | 0
BHGV0035 | 2019-11-12 09:28 | 61.2 | 41.8 | 0.1 | 0 | 980 | -0.48 | 1 | 0
BHGV0036 | 2019-11-12 09:31 | 36.2 | 30.2 | 0.1 | 33.5 | 981 | -4.97 | 0 | 0
BHGV0036 | 2019-11-12 09:31 | 36.3 | 30 | 0.1 | 33.6 | 981 | -0.54 | 0 | 0
BHGV0037 | 2019-11-12 09:33 | 33.4 | 28.7 | 1.5 | 36.4 | 980 | -2.07 | 0 | 0
BHGV0037 | 2019-11-12 09:33 | 32.9 | 28.9 | 1.1 | 37.1 | 980 | -0.87 | 0 | 0
BHM010MB | 2019-11-12 09:35 | 55.7 | 39.8 | 0.8 | 3.7 | 980 | -24.21 | 2 | 0
BHGV0018 | 2019-11-12 09:36 | 59.5 | 41.9 | 0.4 | 0 | 980 | -24.78 | 3 | 0
BHLC004B | 2019-11-12 09:37 | 8.9 | 8.8 | 13.8 | 68.5 | 980 | 1.2 | 7 | 0
BHR0004B | 2019-11-12 09:40 | 0.4 | 8.1 | 13.2 | 78.3 | 980 | 114.51 | 8 | 0
BHGV0015 | 2019-11-12 09:42 | 54 | 40.2 | 1.2 | 4.6 | 980 | -21.83 | 2 | 0
BHGV0014 | 2019-11-12 09:43 | 60.7 | 40.7 | 0.2 | 0 | 980 | -22.41 | 2 | 0
BHGV0014 | 2019-11-12 09:44 | 60.5 | 40.6 | 0.1 | 0 | 980 | -24.56 | 2 | 0
BHGV0013 | 2019-11-12 09:45 | 0.8 | 7 | 12.1 | 80.1 | 980 | -0.68 | 1 | 0
BHGV0016 | 2019-11-12 09:46 | 36.1 | 32.2 | 2 | 29.7 | 980 | -23.48 | 1 | 0
BHGV0016 | 2019-11-12 09:46 | 35.7 | 32.5 | 1.2 | 30.6 | 980 | -1.52 | 1 | 0
BHM010MA | 2019-11-12 09:47 | 58.9 | 40.5 | 0.4 | 0.2 | 980 | -25.98 | 3 | 0
BHL000C4 | 2019-11-12 09:49 | 62.1 | 37 | 0.5 | 0.4 | 980 | 0.99 | 5 | 0
BHL000C4 | 2019-11-12 09:49 | 62.8 | 36.1 | 0.2 | 0.9 | 980 | -0.48 | 4 | 0
BHGV0017 | 2019-11-12 09:51 | 6.5 | 11.6 | 4.6 | 77.3 | 980 | -0.6 | 3 | 0
BHGV0038 | 2019-11-12 09:55 | 51 | 32.1 | 1.4 | 15.5 | 979 | -1.44 | 0 | 0
BHGV0038 | 2019-11-12 09:55 | 50.7 | 31.7 | 1.7 | 15.9 | 980 | -12.56 | 0 | 0
BHGV0039 | 2019-11-12 09:57 | 34.9 | 29.4 | 0.4 | 35.3 | 980 | -26.1 | 0 | 0
BHGV0039 | 2019-11-12 09:57 | 35 | 29 | 0.3 | 35.7 | 980 | -3.28 | 0 | 0
BHGV0010 | 2019-11-12 10:00 | 51.2 | 28.2 | 1.1 | 19.5 | 980 | -23.56 | 0 | 0
BHGV0010 | 2019-11-12 10:00 | 50.3 | 28.5 | 0.4 | 20.8 | 980 | -29.31 | 0 | 0
BHGV0040 | 2019-11-12 10:04 | 56.2 | 34.3 | 0.3 | 9.2 | 981 | 1.69 | 1 | 0
BHGV0040 | 2019-11-12 10:04 | 55.5 | 34.7 | 0.2 | 9.6 | 981 | -0.37 | 0 | 0
BHLC001B | 2019-11-12 10:06 | 55.6 | 32.7 | 2 | 9.7 | 981 | -14.92 | 1 | 0
BHLC001B | 2019-11-12 10:06 | 54.9 | 32.7 | 2 | 10.4 | 981 | -0.34 | 1 | 0
BHGV0009 | 2019-11-12 10:08 | 42 | 31.5 | 0.1 | 26.4 | 981 | -15.81 | 0 | 0
BHGV0041 | 2019-11-12 10:10 | 54.9 | 37.4 | 0.5 | 7.2 | 980 | -9.33 | 0 | 0
BHGV0041 | 2019-11-12 10:10 | 54.7 | 37.5 | 0.2 | 7.6 | 980 | -0.94 | 1 | 0
BHGV0046 | 2019-11-12 10:14 | 58.7 | 40.7 | 0.1 | 0.5 | 979 | 3.07 | 3 | 0
BHGV0046 | 2019-11-12 10:14 | 58.7 | 40.9 | 0.1 | 0.3 | 979 | -2.79 | 3 | 0
BHR0002B | 2019-11-12 10:20 | 60.8 | 37 | 0.6 | 1.6 | 979 | -1.64 | 3 | 0
BHR0002B | 2019-11-12 10:21 | 61 | 37.1 | 0.8 | 1.1 | 979 | 0.08 | 0 | 0
BHLC002B | 2019-11-12 10:25 | 62.7 | 41.1 | 0.6 | 0 | 979 | 4.7 | 2 | 0
BHLC002B | 2019-11-12 10:25 | 62.7 | 41.1 | 0.7 | 0 | 979 | 4.51 | 1 | 0
BHGV0045 | 2019-11-12 10:28 | 63.5 | 40.1 | 0.3 | 0 | 979 | 3.27 | 1 | 0
BHGV0045 | 2019-11-12 10:28 | 62.7 | 40.1 | 0.2 | 0 | 979 | 3.65 | 0 | 0
BHR0001B | 2019-11-12 10:30 | 66.6 | 36.8 | 2.4 | 0 | 979 | 3.81 | 0 | 0
BHR0001B | 2019-11-12 10:30 | 66 | 37.9 | 0.6 | 0 | 979 | -0.43 | 0 | 0
BHGV0043 | 2019-11-12 10:34 | 66.7 | 37.3 | 0.1 | 0 | 980 | 6.62 | 0 | 0
BHGV0043 | 2019-11-12 10:34 | 66.6 | 37.3 | 0.4 | 0 | 980 | 0.01 | 0 | 0
BHGV0007 | 2019-11-12 10:36 | 66.9 | 37.3 | 0.1 | 0 | 980 | 1.74 | 0 | 0
BHGV0007 | 2019-11-12 10:36 | 66.8 | 37.4 | 0 | 0 | 980 | 1.68 | 0 | 0
BHGV0008 | 2019-11-12 10:38 | 23.4 | 13.9 | 10.7 | 52 | 980 | 6.05 | 10 | 0
BHLC002R | 2019-11-12 10:40 | 65.9 | 36.6 | 0.5 | 0 | 980 | 0.19 | 0 | 0
BHLC002R | 2019-11-12 10:40 | 66.1 | 36.9 | 0.3 | 0 | 980 | 1.48 | 0 | 0
BHGV0044 | 2019-11-12 10:41 | 66 | 36.2 | 0.6 | 0 | 980 | 0.48 | 0 | 0
BHGV0004 | 2019-11-12 10:43 | 65.5 | 38.1 | 1.3 | 0 | 980 | 2.86 | 0 | 0
BHGV0004 | 2019-11-12 10:43 | 65.2 | 39 | 0.4 | 0 | 980 | 0.83 | 0 | 0
BHGV0003 | 2019-11-12 10:45 | 69.9 | 35 | 0 | 0 | 980 | 0.3 | 0 | 0
BHGV0003 | 2019-11-12 10:45 | 70 | 35 | 0 | 0 | 980 | 0.57 | 0 | 0
BHGV0006 | 2019-11-12 10:47 | 63.2 | 40.4 | 0.1 | 0 | 980 | 0.98 | 1 | 0
BHGV0045 | 2019-11-12 10:49 | 61.8 | 39.1 | 0.1 | 0 | 981 | 3.85 | 0 | 0
BHGV0026 | 2019-11-12 10:53 | 63 | 41 | 0.2 | 0 | 979 | 5.22 | 2 | 0
BHGV0027 | 2019-11-12 10:55 | 62.5 | 41.6 | 0.6 | 0 | 979 | 4.48 | 1 | 0
BHGV0028 | 2019-11-12 10:58 | 0.2 | 2.1 | 16.1 | 81.6 | 979 | -0.99 | 0 | 0
BHGV0029 | 2019-11-12 11:02 | 59.8 | 37.5 | 0.2 | 2.5 | 979 | 0.09 | 0 | 0
BHGV000C | 2019-11-12 11:04 | 60.2 | 40.3 | 0.1 | 0 | 979 | 0.24 | 2 | 1
BHR00005 | 2019-11-12 11:06 | 0.2 | 4 | 16.3 | 79.5 | 979 | 12.95 | 0 | 0
BHGV0031 | 2019-11-12 11:08 | 64.5 | 38.3 | 0.2 | 0 | 979 | 1.12 | 0 | 0
BHLC0005 | 2019-11-12 11:09 | 59.1 | 40.7 | 0.6 | 0 | 979 | 0.57 | 1 | 0
BHR0006B | 2019-11-12 11:12 | 56.3 | 40.4 | 0.5 | 2.8 | 979 | 3.16 | 1 | 0
BHLC0006 | 2019-11-12 11:15 | 68.9 | 38.8 | 0.2 | 0 | 979 | 1.43 | 0 | 0
BHGV0033 | 2019-11-12 11:17 | 56.2 | 34.9 | 0.9 | 8 | 979 | 1.89 | 0 | 0
BHGV0049 | 2019-11-12 11:19 | 47.2 | 29.8 | 0.5 | 22.5 | 979 | 0.68 | 0 | 0
BHGW0034 | 2019-11-12 11:21 | 22.3 | 11.1 | 7.2 | 59.4 | 979 | 0.19 | 0 | 0
BHG010MA | 2019-11-12 11:27 | 52.5 | 36.3 | 1 | 10.2 | 981 | -24.15 | 1 | 0
BHG01MDA | 2019-11-12 11:30 | 52.8 | 35.8 | 1.1 | 10.3 | 980 | 175.47 | 0 | 0

## December 2019
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-12-06
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 17.3 | 82.2 | 0 | 0 | 1003 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.4 | 11.4 | 86.1 | 0 | 0 | 1003 | 0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.7 | 19.9 | 79.4 | 0 | 0 | 1004 | -0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 19.6 | 79.7 | 0 | 0 | 1004 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 1004 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.8 | 19.5 | 79.7 | 0 | 0 | 1004 | 0 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.6 | 3.1 | 14.3 | 74 | 0 | 0 | 1004 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.8 | 6.7 | 13.6 | 68.9 | 0 | 0 | 1003 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.7 | 0.9 | 19 | 79.4 | 0 | 0 | 1004 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.4 | 0.6 | 18.5 | 80.5 | 0 | 0 | 1004 | 0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 5.5 | 7.4 | 87 | 0 | 0 | 1004 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.5 | 18.2 | 81.3 | 0 | 0 | 1004 | 0.1 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 1004 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.4 | 82.4 | 0 | 0 | 1004 | 0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.3 | 15.9 | 83.7 | 0 | 0 | 1004 | -0.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1004 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 5.3 | 6.9 | 87.7 | 0 | 0 | 1004 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.5 | 18.7 | 78.8 | 0 | 0 | 1004 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 3.1 | 13.2 | 83.6 | 0 | 0 | 1004 | 0.45 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.9 | 12.2 | 82.9 | 0 | 0 | 1003 | -0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1003 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.1 | 16.4 | 82.4 | 0 | 0 | 1004 | 0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-12-12
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 959 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.4 | 17.4 | 80.2 | 0 | 0 | 960 | 0.94 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.7 | 19.8 | 79.5 | 0 | 0 | 960 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 19.5 | 79.8 | 0 | 0 | 960 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 960 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 20.8 | 79.1 | 0 | 0 | 960 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.8 | 0.9 | 18 | 80.3 | 0 | 0 | 960 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 5.1 | 3.2 | 15.7 | 76 | 0 | 0 | 960 | 0.12 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.7 | 18.2 | 80.1 | 0 | 0 | 960 | -0.65 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0.5 | 18.4 | 80.8 | 0 | 0 | 960 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.6 | 17.2 | 82.2 | 0 | 0 | 960 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 18.5 | 81.3 | 0 | 0 | 960 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 2.4 | 17.7 | 79.8 | 0 | 0 | 960 | -0.18 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 1.8 | 17.9 | 80.2 | 0 | 0 | 960 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 2 | 15.8 | 81.6 | 0 | 0 | 958 | -0.36 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.8 | 17.3 | 80.9 | 0 | 0 | 958 | -0.36 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 21.2 | 78.8 | 0 | 0 | 958 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.2 | 18.5 | 79.3 | 0 | 0 | 959 | 0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.9 | 19.9 | 79.2 | 0 | 0 | 958 | -0.89 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.1 | 18.5 | 81.4 | 0 | 0 | 959 | -0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 18.5 | 81.4 | 0 | 0 | 960 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 4.4 | 14.3 | 81.2 | 0 | 0 | 959 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-12-20
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 19 | 80.8 | 0 | 0 | 968 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.4 | 17.4 | 80.2 | 0 | 0 | 968 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.6 | 19.7 | 79.7 | 0 | 0 | 968 | -0.03 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 968 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 19.7 | 79.9 | 0 | 0 | 968 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 20.8 | 79.1 | 0 | 0 | 969 | -0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.8 | 0.9 | 18 | 80.3 | 0 | 0 | 969 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.5 | 3 | 17.4 | 75.1 | 0 | 0 | 968 | 0.12 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 18.5 | 80.3 | 0 | 0 | 969 | -0.65 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.4 | 18.2 | 81.2 | 0 | 0 | 969 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.5 | 17 | 82.5 | 0 | 0 | 969 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 18.2 | 81.5 | 0 | 0 | 969 | 0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 19.2 | 80.7 | 0 | 0 | 970 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 18.7 | 80.8 | 0 | 0 | 969 | 0 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 1.3 | 17.9 | 80.8 | 0 | 0 | 969 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 19.2 | 80.8 | 0 | 0 | 968 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 9.2 | 2.1 | 88.7 | 0 | 0 | 969 | 0.29 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.1 | 18.4 | 79.5 | 0 | 0 | 969 | 0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried |  |  |  | 100 |  |  |  |  | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 1.6 | 17.3 | 81 | 0 | 0 | 969 | 0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 5.9 | 12.8 | 81.2 | 0 | 0 | 969 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 19 | 81 | 0 | 0 | 968 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1 | 18.3 | 80.7 | 0 | 0 | 968 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2019-12-27
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 1015 | -0.03 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.9 | 11.9 | 86.1 | 0 | 0 | 1014 | -0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 19.5 | 80.2 | 0 | 0 | 1014 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.4 | 19.4 | 80.2 | 0 | 0 | 1014 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 19.6 | 79.9 | 0 | 0 | 1014 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 20.5 | 79.4 | 0 | 0 | 1014 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.9 | 2.8 | 15.2 | 75.1 | 0 | 0 | 1014 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.1 | 7 | 14.1 | 68.8 | 0 | 0 | 1014 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 18.4 | 80.3 | 0 | 0 | 1014 | -0.55 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.5 | 18.3 | 81 | 0 | 0 | 1014 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.1 | 7.6 | 87.3 | 0 | 0 | 1015 | 0.07 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1015 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1014 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1015 | -0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.2 | 16.4 | 83.3 | 0 | 0 | 1015 | 0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1015 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.7 | 7.5 | 87.8 | 0 | 0 | 1015 | -0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.2 | 18.8 | 79 | 0 | 0 | 1015 | 0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.9 | 17.4 | 80.7 | 0 | 0 | 1014 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.2 | 13.1 | 82.7 | 0 | 0 | 1014 | -0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 1014 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.8 | 17 | 82.2 | 0 | 0 | 1014 | 0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).

## January 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-01-02
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 17.9 | 81.9 | 0 | 0 | 1003 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.5 | 12.5 | 85.8 | 0 | 0 | 1002 | -0.14 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.7 | 2.9 | 15.8 | 73.6 | 0 | 0 | 1002 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.9 | 7.4 | 13.3 | 68.4 | 0 | 0 | 1002 | 0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.4 | 18.5 | 80.9 | 0 | 0 | 1002 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.5 | 7.2 | 87.3 | 0 | 0 | 1002 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 1003 | 0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.3 | 17.1 | 82.5 | 0 | 0 | 1002 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.2 | 16.4 | 83.3 | 0 | 0 | 1002 | -0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1002 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.1 | 7.9 | 88 | 0 | 0 | 1002 | 0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 | Buried | [8 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.6 | 17.4 | 81 | 0 | 0 | 1014 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.6 | 13.6 | 82.8 | 0 | 0 | 1002 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1002 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 17.5 | 82 | 0 | 0 | 1003 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-01-09
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.2 | 17.3 | 82.3 | 0 | 0 | 988 | 0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.3 | 1.6 | 13.7 | 84.4 | 0 | 0 | 988 | 0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.8 | 3 | 14.4 | 73.8 | 0 | 0 | 989 | 0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.7 | 8.1 | 13.8 | 66.4 | 0 | 0 | 988 | 0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.4 | 18.5 |  | 0 | 0 | 988 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.8 | 6.5 | 87.7 | 0 | 0 | 988 | -0.01 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 988 | 0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 17.4 | 82.3 | 0 | 0 | 988 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.3 | 16.1 | 83.6 | 0 | 0 | 988 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.4 | 17.2 | 82.3 | 0 | 0 | 988 | -0.13 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.6 | 7.5 | 87.9 | 0 | 0 | 988 | 0.2 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.7 | 17.3 | 81 | 0 | 0 | 988 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.3 | 13.2 | 83.5 | 0 | 0 | 988 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 988 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 988 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-01-17
Weather: | dry
Wind conditions: | slight Breeze
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 17.7 | 81.8 | 0 | 0 | 999 | -0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.3 | 14.4 | 84.2 | 0 | 0 | 999 | 0.16 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.1 | 2.7 | 15.2 | 74 | 0 | 0 | 999 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.5 | 8.8 | 12.6 | 66.1 | 0 | 0 | 999 | 0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.3 | 0.5 | 18.2 | 81 | 0 | 0 | 999 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.1 | 6.8 | 88.1 | 0 | 0 | 999 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 999 | 0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 999 | 0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 999 | -0.13 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 999 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4.1 | 7.9 | 88 | 0 | 0 | 999 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.6 | 17.3 | 81.1 | 0 | 0 | 999 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.9 | 13.8 | 83.3 | 0 | 0 | 999 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 999 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 999 | -0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-01-21
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.3 | 17.3 | 82.3 | 0 | 0 | 1030 | 0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 1.8 | 14.1 | 83.9 | 0 | 0 | 1030 | -0.17 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9 | 2.9 | 14.8 | 73.3 | 0 | 0 | 1029 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.9 | 8.5 | 13.1 | 65.5 | 0 | 0 | 1030 | -0.31 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.4 | 18 | 81.4 | 0 | 0 | 1029 | 0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.4 | 7.5 | 88.1 | 0 | 0 | 1030 | 0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18 | 81.9 | 0 | 0 | 1029 | 0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1029 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.2 | 17.6 | 82.1 | 0 | 0 | 1029 | 0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 17.1 | 82.5 | 0 | 0 | 1029 | -0.14 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 3.3 | 8.5 | 88.2 | 0 | 0 | 1029 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.5 | 17.3 | 81.2 | 0 | 0 | 1029 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 14.4 | 83.4 | 0 | 0 | 1030 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.2 | 17.2 | 82.5 | 0 | 0 | 1030 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.1 | 18.2 | 81.7 | 0 | 0 | 1030 | -0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-01-27
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 18.3 | 81.5 | 0 | 0 | 973 | 0 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.1 | 18.3 | 81.5 | 0 | 0 | 974 | 1.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.7 | 2.5 | 14.7 | 74.1 | 0 | 0 | 974 | 0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 6.7 | 4.1 | 15.9 | 73.3 | 0 | 0 | 974 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 0.3 | 18.2 | 81.3 | 0 | 0 | 974 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.2 | 7.3 | 88.5 | 0 | 0 | 974 | 0.12 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 18.2 | 81.7 | 0 | 0 | 973 | 0.2 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.1 | 18.4 | 81.4 | 0 | 0 | 973 | 0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.5 | 0.5 | 17.1 | 81.9 | 0 | 0 | 973 | 0.21 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 17.5 | 82.3 | 0 | 0 | 973 | -0.21 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.5 | 3.5 | 8.3 | 87.7 | 0 | 0 | 973 | -1.22 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 1.1 | 17.9 | 80.9 | 0 | 0 | 973 | -0.23 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 5 | 13 | 81.9 | 0 | 0 | 973 | -0.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0 | 18.1 | 81.8 | 0 | 0 | 973 | -0.19 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.8 | 16.9 | 81.2 | 0 | 0 | 973 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA10078 | MCERTS certified instrument
Date downloaded | 2020-01-10 19:36 | Software Version | 1.10.0
Computer & User Info | NP-CNU03950XR-E | mark.johnstone
Date of last user calibration | 2019-12-31
Date of last factory calibration | 2019-10-03
Next service due | 2020-04-07
Date of last Gas Check | 2019-10-03
Security code | [31717DC8]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-01-10 14:44 | 54 | 37.1 | 1.2 | 7.7 | 1003 | 203.95 | 1 | 0
BHG010MB | 2020-01-10 14:48 | 54 | 37.7 | 1.2 | 7.1 | 1003 | -4.39 | 1 | 0
BHGV0035 | 2020-01-10 14:48 | 62.5 | 40.3 | 0.5 | 0 | 1002 | -1.04 | 1 | 0
BHGV0035 | 2020-01-10 14:48 | 62.4 | 41.1 | 0 | 0 | 1002 | -1.43 | 1 | 0
BHGV0036 | 2020-01-10 14:49 | 51.3 | 34.7 | 0 | 14 | 1003 | -1.73 | 0 | 0
BHGV0037 | 2020-01-10 14:51 | 35.1 | 30.7 | 1 | 33.2 | 1003 | -0.63 | 0 | 0
BHGV0037 | 2020-01-10 14:51 | 35.2 | 30.5 | 1.1 | 33.2 | 1003 | 0.4 | 0 | 0
BHM010MB | 2020-01-10 14:52 | 61 | 41 | 0.1 | 0 | 1003 | -2.68 | 1 | 0
BHGV0018 | 2020-01-10 14:53 | 59.6 | 43.6 | 0 | 0 | 1003 | -2.71 | 3 | 0
BHLC004B | 2020-01-10 14:54 | 2.1 | 7.4 | 15.4 | 75.1 | 1003 | 0.38 | 4 | 0
BHR0004B | 2020-01-10 14:56 | 3.2 | 5.4 | 16.1 | 75.3 | 1003 | 0.41 | 2 | 0
BHGV0015 | 2020-01-10 14:57 | 61.3 | 41.1 | 0.5 | 0 | 1003 | -2.72 | 2 | 1
BHGV0014 | 2020-01-10 14:58 | 60.9 | 42.4 | 0 | 0 | 1003 | -2.69 | 2 | 1
BHGV0014 | 2020-01-10 14:58 | 61 | 42.5 | 0 | 0 | 1003 | -2.68 | 2 | 1
BHGV0013 | 2020-01-10 15:00 | 21.2 | 15.2 | 11.2 | 52.4 | 1003 | 0.47 | 0 | 0
BHGV0016 | 2020-01-10 15:01 | 59.7 | 38.3 | 0 | 2 | 1003 | -2.33 | 4 | 0
BHGV0016 | 2020-01-10 15:02 | 59.7 | 38.3 | 0 | 2 | 1003 | -2.55 | 3 | 0
BHM010MA | 2020-01-10 15:03 | 60.6 | 40.9 | 0.3 | 0 | 1003 | -2.69 | 2 | 0
BHL000C4 | 2020-01-10 15:04 | 2.5 | 13.6 | 9.3 | 74.6 | 1003 | 0.37 | 1 | 0
BHGV0038 | 2020-01-10 15:07 | 43.9 | 28.9 | 2.9 | 24.3 | 1002 | -3.45 | 0 | 0
BHGV0039 | 2020-01-10 15:09 | 64.7 | 32 | 1.6 | 1.7 | 1003 | -0.76 | 0 | 0
BHGV0039 | 2020-01-10 15:10 | 64.3 | 32.3 | 1.3 | 2.1 | 1003 | -2.8 | 0 | 0
BHGV0011 | 2020-01-10 15:11 | 48 | 25.2 | 0 | 26.8 | 1003 | -0.97 | 0 | 0
BHGV0010 | 2020-01-10 15:14 | 37.8 | 25.4 | 0 | 36.8 | 1004 | -2.32 | 0 | 0
BHGV0010 | 2020-01-10 15:14 | 37.8 | 26.3 | 0 | 35.9 | 1004 | -0.28 | 0 | 0
BHGV0040 | 2020-01-10 15:15 | 57 | 32.5 | 0.3 | 10.2 | 1004 | -2.55 | 0 | 0
BHGV0040 | 2020-01-10 15:15 | 56 | 33.3 | 0 | 10.7 | 1004 | -2.88 | 0 | 0
BHGV0009 | 2020-01-10 15:16 | 65.5 | 35.3 | 0.3 | 0 | 1004 | -3.09 | 0 | 0
BHGV0009 | 2020-01-10 15:16 | 65.4 | 36.1 | 0 | 0 | 1004 | -3.23 | 0 | 0
BHLC0003 | 2020-01-10 15:20 | 1.6 | 4.1 | 17.1 | 77.2 | 1003 | 0.09 | 0 | 0
BHGV0301 | 2020-01-10 15:23 | 65.6 | 36 | 0.4 | 0 | 1003 | -3.04 | 1 | 0
BHGV0012 | 2020-01-10 15:25 | 61.1 | 41.7 | 0.5 | 0 | 1003 | -2.66 | 1 | 2
BHR00003 | 2020-01-10 15:26 | 8.8 | 14.6 | 6.1 | 70.5 | 1002 | -0.88 | 0 | 0
BHGV0046 | 2020-01-10 15:28 | 60.9 | 42.6 | 0.3 | 0 | 1002 | -0.22 | 1 | 0
BHGV0046 | 2020-01-10 15:28 | 59.5 | 43.1 | 0 | 0 | 1002 | -2.1 | 2 | 0
BHGV0041 | 2020-01-10 15:29 | 61.2 | 41.6 | 0 | 0 | 1002 | -2.83 | 1 | 0
BHGV0041 | 2020-01-10 15:29 | 61.7 | 41.4 | 0 | 0 | 1002 | -2.97 | 1 | 0
BHGV0042 | 2020-01-10 15:32 | 13.7 | 8.7 | 13.3 | 64.3 | 1003 | -1.36 | 1 | 0
BHGV0042 | 2020-01-10 15:36 | 15.6 | 9.2 | 11.4 | 63.8 | 1003 | 0.19 | 0 | 0
BHGV0043 | 2020-01-10 15:38 | 65.1 | 36.9 | 0.9 | 0 | 1003 | -3.53 | 0 | 0
BHGV0043 | 2020-01-10 15:38 | 60.6 | 37.8 | 0.3 | 1.3 | 1003 | -3.6 | 0 | 0
BHGV0007 | 2020-01-10 15:39 | 56.8 | 33.6 | 1.6 | 8 | 1003 | -4.3 | 0 | 0
BHGV0008 | 2020-01-10 15:41 | 7.3 | 7.7 | 14.4 | 70.6 | 1004 | -7 | 11 | 0
BHLC002R | 2020-01-10 15:42 | 66.8 | 36.4 | 0.7 | 0 | 1003 | -3.4 | 0 | 0
BHLC002R | 2020-01-10 15:42 | 65.8 | 37.4 | 0 | 0 | 1003 | -3.45 | 0 | 0
BHGV0044 | 2020-01-10 15:45 | 54.5 | 38.8 | 0.5 | 6.2 | 1003 | -3.16 | 0 | 0
BHR00001 | 2020-01-10 15:46 | 67.2 | 35.9 | 0.3 | 0 | 1002 | 0.18 | 0 | 0
BHR00001 | 2020-01-10 15:46 | 67.3 | 35.6 | 0.2 | 0 | 1002 | -2.92 | 0 | 0
BHGV0001 | 2020-01-10 15:49 | 64.4 | 39.2 | 0 | 0 | 1002 | -2.84 | 0 | 0
BHGV0045 | 2020-01-10 15:50 | 63.4 | 40.7 | 0 | 0 | 1002 | -2.88 | 0 | 0
BHLC002B | 2020-01-10 15:53 | 52 | 36.5 | 2.2 | 9.3 | 1002 | -2.31 | 0 | 0
BHGV0026 | 2020-01-10 16:01 | 62.8 | 41.2 | 0.4 | 0 | 1002 | -2.91 | 1 | 3
BHR0002B | 2020-01-10 16:03 | 7.6 | 28.1 | 0 | 64.3 | 1001 | 0.46 | 8 | 0
BHGV0027 | 2020-01-10 16:05 | 60.9 | 42.6 | 0 | 0 | 1002 | -2.81 | 2 | 0
BHGV0047 | 2020-01-10 16:08 | 57.4 | 38.9 | 1 | 2.7 | 1002 | -0.09 | 1 | 0
BHGV0047 | 2020-01-10 16:09 | 57.1 | 39 | 1 | 2.9 | 1002 | -0.48 | 1 | 0
BHGV0048 | 2020-01-10 16:12 | 61 | 42.5 | 0 | 0 | 1002 | -3.04 | 1 | 0
BHLC0006 | 2020-01-10 16:14 | 23.9 | 20.6 | 8.1 | 47.4 | 1002 | -0.12 | 1 | 0
BHLC006B | 2020-01-10 16:16 | 60.1 | 41.6 | 0.8 | 0 | 1001 | 2.81 | 1 | 0
BHLC006B | 2020-01-10 16:17 | 59.5 | 42.4 | 0.5 | 0 | 1001 | 0 | 1 | 0
BHLC0005 | 2020-01-10 16:22 | 20.5 | 22.9 | 7.2 | 49.4 | 1001 | -0.13 | 1 | 0
BHLC0005 | 2020-01-10 16:23 | 20.5 | 21.1 | 9.7 | 48.7 | 1001 | 0.17 | 0 | 0
BHGV0049 | 2020-01-10 16:30 | 63.4 | 40.6 | 0.3 | 0 | 1002 | -0.44 | 0 | 0
BHGV0049 | 2020-01-10 16:32 | 63 | 40.8 | 0 | 0 | 1002 | -3.14 | 0 | 0
BHG010MA | 2020-01-10 16:37 | 54.9 | 38.4 | 1.1 | 5.6 | 1003 | -4.73 | 0 | 0
BHG01MDA | 2020-01-10 16:40 | 55.6 | 37.8 | 1.1 | 5.5 | 1003 | 204.24 | 0 | 0
Model | GA2000Plus | Serial No | GA12599 | MCERTS certified instrument
Date downloaded | 2020-01-17 16:58 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-01-06
Date of last factory calibration | 2019-11-23
Next service due | 2020-05-23
Date of last Gas Check | 2019-11-23
Security code | [502E48D4]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-01-17 14:12 | 57.9 | 39.1 | 0.7 | 2.3 | 998 | 197.18 | 0 | 0
BHG010MB | 2020-01-17 14:14 | 57.9 | 38.7 | 0.7 | 2.7 | 997 | -6.6 | 1 | 0
BHGV0025 | 2020-01-17 14:18 | 62.6 | 37.8 | 0.2 | 0 | 997 | -0.31 | 0 | 0
BHGV0026 | 2020-01-17 14:20 | 33.6 | 19.3 | 3.8 | 43.3 | 997 | 0.89 | 19 | 0
BHGV0024 | 2020-01-17 14:21 | 63.9 | 41.3 | 0.5 | 0 | 998 | -3.61 | 0 | 0
BHGV0023 | 2020-01-17 14:22 | 64.1 | 40.9 | 0.2 | 0 | 997 | -0.18 | 0 | 0
BHGV0048 | 2020-01-17 14:25 | 60.5 | 42 | 0.2 | 0 | 997 | -4.95 | 0 | 0
BHGV0024 | 2020-01-17 14:28 | 2.2 | 8.3 | 11.2 | 78.3 | 997 | 0.23 | 0 | 0
BHGV0004 | 2020-01-17 14:30 | 67.3 | 34.7 | 0.1 | 0 | 997 | -5.47 | 0 | 0
BHGV0004 | 2020-01-17 14:30 | 66.5 | 34.7 | 0.5 | 0 | 997 | -0.3 | 0 | 0
BHGV0003 | 2020-01-17 14:32 | 69.8 | 35.9 | 0 | 0 | 998 | -4.95 | 0 | 0
BHGV0003 | 2020-01-17 14:32 | 69.8 | 35.9 | 0 | 0 | 998 | -4.99 | 6 | 0
BHGV0045 | 2020-01-17 14:34 | 65.9 | 39.3 | 0.1 | 0 | 998 | -4.86 | 0 | 0
BHR00001 | 2020-01-17 14:35 | 0.6 | 4.7 | 14.7 | 80 | 998 | -1.8 | 0 | 0
BHR0001B | 2020-01-17 14:40 | 66.7 | 38.4 | 0.5 | 0 | 998 | -3.21 | 0 | 0
BHGV0027 | 2020-01-17 14:51 | 61.2 | 42.7 | 0.7 | 0 | 996 | -4.57 | 0 | 0
BHGV0028 | 2020-01-17 14:53 | 60.2 | 45 | 0.1 | 0 | 996 | -3.25 | 4 | 0
BHGV0028 | 2020-01-17 14:53 | 60.1 | 45.2 | 0 | 0 | 996 | -0.2 | 0 | 0
BHGV0029 | 2020-01-17 14:55 | 64.2 | 41.2 | 0.3 | 0 | 996 | -4.79 | 0 | 0
BHGV0031 | 2020-01-17 14:58 | 62.8 | 42 | 0.5 | 0 | 996 | -4.42 | 0 | 0
BHLC0005 | 2020-01-17 15:01 | 59.5 | 44.7 | 0.1 | 0 | 996 | -0.82 | 4 | 0
BHLC0005 | 2020-01-17 15:02 | 59.5 | 44.7 | 0.1 | 0 | 996 | -0.04 | 0 | 0
BHGV0032 | 2020-01-17 15:04 | 61.3 | 44 | 0.5 | 0 | 997 | -0.15 | 1 | 0
BHGV0033 | 2020-01-17 15:06 | 62.1 | 40.8 | 0.1 | 0 | 996 | -4.34 | 1 | 0
BHG010MA | 2020-01-17 15:09 | 58.8 | 38.9 | 0.8 | 1.5 | 997 | -6.45 | 1 | 0
BHG01MDA | 2020-01-17 15:12 | 58.1 | 39.6 | 0.8 | 1.5 | 997 | 198.46 | 2 | 0

## February 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-02-05
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 1000 | 0.1 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.1 | 13.9 | 84 | 0 | 0 | 1000 | 0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 1000 | -1.27 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0 | 0 | 18.7 | 81.3 | 0 | 0 | 1000 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 6.8 | 4.4 | 16.4 | 72.4 | 0 | 0 | 1000 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.4 | 18 | 81.5 | 0 | 0 | 1000 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.9 | 7.1 | 89 | 0 | 0 | 1000 | 0.1 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 1000 | 0.15 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0 | 18.7 | 81.3 | 0 | 0 | 1000 | -0.19 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.3 | 18.2 | 81.4 | 0 | 0 | 1000 | -0.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 18.4 | 81.4 | 0 | 0 | 1000 | 0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 18.4 | 81.6 | 0 | 0 | 1000 | 0.31 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 1000 | 0.28 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 3.3 | 17 | 79.6 | 0 | 0 | 1000 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 1000 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 17.4 | 80.9 | 0 | 0 | 1000 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-02-12
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.8 | 81.9 | 0 | 0 | 996 | 0.03 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 13.6 | 84.2 | 0 | 0 | 995 | -0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 995 | -1.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.2 | 2.2 | 15.8 | 78.8 | 0 | 0 | 996 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.8 | 8 | 13.7 | 67.5 | 0 | 0 | 996 | -0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.4 | 18 | 81.5 | 0 | 0 | 996 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.4 | 17.5 | 78.1 | 0 | 0 | 997 | -0.25 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18 | 81.9 | 0 | 0 | 996 | -0.13 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 17.9 | 82 | 0 | 0 | 996 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 996 | -0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 18.5 | 81.4 | 0 | 0 | 996 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 15.2 | 83.7 | 0 | 0 | 996 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 996 | 0.25 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 16.7 | 80.8 | 0 | 0 | 996 | -0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 996 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1 | 17.9 | 81.1 | 0 | 0 | 996 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-02-22
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 985 | 0.1 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.1 | 13.9 | 84 | 0 | 0 | 985 | 0.08 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18.4 | 81.6 | 0 | 0 | 985 | -0.88 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.8 | 0.9 | 18 | 80.3 | 0 | 0 | 985 | 0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.5 | 3 | 17.4 | 75.1 | 0 | 0 | 985 | -0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.3 | 18.1 | 81.5 | 0 | 0 | 985 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 4.2 | 17.9 | 77.9 | 0 | 0 | 985 | -0.22 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 19 | 81 | 0 | 0 | 985 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 18.9 | 81 | 0 | 0 | 985 | -0.19 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 1.9 | 15.9 | 81.6 | 0 | 0 | 985 | -0.08 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 19 | 80.6 | 0 | 0 | 984 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 21.2 | 78.8 | 0 | 0 | 984 | -0.24 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.1 | 81.9 | 0 | 0 | 984 | 0.24 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.1 | 18.5 | 81.4 | 0 | 0 | 984 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 18.6 | 81.4 | 0 | 0 | 985 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 4.4 | 14.3 | 81.2 | 0 | 0 | 985 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-02-27
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 18.3 | 81.6 | 0 | 0 | 987 | -0.07 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.8 | 14.9 | 83.3 | 0 | 0 | 988 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18 | 82 | 0 | 0 | 988 | -0.86 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.7 | 2.4 | 14.1 | 79.8 | 0 | 0 | 987 | -0.09 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.3 | 7.1 | 14 | 67.6 | 0 | 0 | 988 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.2 | 18 | 81.7 | 0 | 0 | 987 | 0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.9 | 7.3 | 88.8 | 0 | 0 | 987 | 0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 988 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 987 | -0.01 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.1 | 18.4 | 81.5 | 0 | 0 | 987 | 0.06 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 987 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.3 | 14.7 | 84 | 0 | 0 | 987 | -0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.3 | 81.7 | 0 | 0 | 987 | 0.22 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 17.3 | 80.5 | 0 | 0 | 987 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 17.8 | 81.8 | 0 | 0 | 987 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.7 | 18.2 | 81.1 | 0 | 0 | 988 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12599 | MCERTS certified instrument
Date downloaded | 2020-02-12 17:20 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-01-06
Date of last factory calibration | 2019-11-23
Next service due | 2020-05-23
Date of last Gas Check | N/A
Security code | [073A1827]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-02-12 09:57 | 55.1 | 34.4 | 1.1 | 9.4 | 998 | 197.94 | 1 | 0
BHG010MB | 2020-02-12 10:00 | 55.5 | 34 | 1 | 9.5 | 996 | -8.42 | 1 | 0
BHGV0035 | 2020-02-12 10:03 | 63.1 | 37.7 | 0.4 | 0 | 996 | -5.47 | 1 | 0
BHGV0035 | 2020-02-12 10:03 | 61.7 | 38 | 0.9 | 0 | 996 | -1.24 | 1 | 0
BHGV0036 | 2020-02-12 10:04 | 50.4 | 30 | 0.1 | 19.5 | 996 | -5.16 | 0 | 0
BHGV0036 | 2020-02-12 10:05 | 50 | 30.1 | 0.1 | 19.8 | 996 | -1.22 | 0 | 0
BHGV0037 | 2020-02-12 10:06 | 68.8 | 32.8 | 0.1 | 0 | 997 | -2.67 | 0 | 0
BHGV0037 | 2020-02-12 10:07 | 68.6 | 32.9 | 0.1 | 0 | 997 | -1.2 | 0 | 0
BHM010MB | 2020-02-12 10:08 | 59.6 | 39.8 | 0.1 | 0.5 | 997 | -8.4 | 5 | 0
BHGV0018 | 2020-02-12 10:10 | 59.8 | 40.5 | 0.2 | 0 | 996 | -6.52 | 4 | 0
BHLC004B | 2020-02-12 10:12 | 1.5 | 4.2 | 15 | 79.3 | 996 | -0.03 | 3 | 0
BHR0004B | 2020-02-12 10:14 | 0.2 | 2.8 | 16 | 81 | 996 | 258.3 | 0 | 0
BHGV0015 | 2020-02-12 10:16 | 59.3 | 40.3 | 0.4 | 0 | 997 | -5.19 | 3 | 0
BHGV0014 | 2020-02-12 10:17 | 59.8 | 39.1 | 0.2 | 0.9 | 997 | -5.39 | 3 | 0
BHGV0013 | 2020-02-12 10:19 | 16.3 | 10.6 | 11.6 | 61.5 | 996 | -0.05 | 0 | 0
BHGV0016 | 2020-02-12 10:21 | 60.8 | 37.5 | 0.3 | 1.4 | 997 | -5.34 | 4 | 0
BHGV0016 | 2020-02-12 10:21 | 60.2 | 37.7 | 0.4 | 1.7 | 997 | -0.77 | 3 | 0
BHM010MA | 2020-02-12 10:24 | 59.5 | 40.2 | 0.3 | 0 | 997 | -3.36 | 3 | 0
BHL000C4 | 2020-02-12 10:26 | 50.5 | 29.7 | 1.9 | 17.9 | 997 | 0.52 | 7 | 0
BHL000C4 | 2020-02-12 10:26 | 50.8 | 29.7 | 1.8 | 17.7 | 997 | -0.17 | 7 | 0
BHGV0017 | 2020-02-12 10:28 | 31.1 | 28.2 | 5.2 | 35.5 | 996 | 1.1 | 0 | 0
BHGV0038 | 2020-02-12 10:32 | 11.6 | 8.4 | 12.5 | 67.5 | 996 | -1.78 | 0 | 0
BHGV0038 | 2020-02-12 10:32 | 11.6 | 8.5 | 12.4 | 67.5 | 996 | -0.02 | 0 | 0
BHGV0039 | 2020-02-12 10:36 | 57.6 | 29.6 | 0.5 | 12.3 | 997 | -4.32 | 0 | 0
BHGV0039 | 2020-02-12 10:36 | 57.5 | 29.9 | 0.2 | 12.4 | 997 | -0.07 | 0 | 0
BHGV0011 | 2020-02-12 10:38 | 39.9 | 28.2 | 0.5 | 31.4 | 998 | -1.39 | 0 | 0
BHGV0011 | 2020-02-12 10:38 | 39.9 | 28.6 | 0.1 | 31.4 | 998 | -0.3 | 0 | 0
BHGV0010 | 2020-02-12 10:40 | 59.4 | 27.5 | 0.2 | 12.9 | 998 | -3.39 | 0 | 0
BHGV0040 | 2020-02-12 10:41 | 55.6 | 32.6 | 0.2 | 11.6 | 998 | -4.43 | 0 | 0
BHGV0040 | 2020-02-12 10:42 | 55.7 | 32.9 | 0 | 11.4 | 998 | -0.26 | 0 | 0
BHLC001B | 2020-02-12 10:44 | 31 | 19.3 | 7.6 | 42.1 | 931 | -3.75 | 0 | 0
BHLC001B | 2020-02-12 10:44 | 31 | 19.3 | 7.4 | 42.3 | 931 | 0.11 | 0 | 0
BHGV0009 | 2020-02-12 10:46 | 57.8 | 29 | 0.1 | 13.1 | 998 | -4.8 | 0 | 0
BHGV0009 | 2020-02-12 10:47 | 57.6 | 29 | 0.9 | 12.5 | 998 | 0.19 | 0 | 0
BHGV0042 | 2020-02-12 10:53 | 4.4 | 4.1 | 13.7 | 77.8 | 998 | -1.18 | 0 | 0
BHGV0043 | 2020-02-12 10:55 | 56.4 | 31.3 | 0.1 | 12.2 | 998 | -4.56 | 0 | 0
BHGV0043 | 2020-02-12 10:55 | 55.9 | 31.6 | 0.8 | 11.7 | 998 | -0.35 | 0 | 0
BHGV0007 | 2020-02-12 10:58 | 63.3 | 26.7 | 2.9 | 7.1 | 998 | -4.62 | 0 | 0
BHGV0007 | 2020-02-12 10:58 | 62.6 | 27.3 | 2.2 | 7.9 | 998 | -0.13 | 0 | 0
BHGV0008 | 2020-02-12 11:01 | 24.8 | 16.3 | 7.5 | 51.4 | 998 | -1.7 | 5 | 0
BHLC002R | 2020-02-12 11:05 | 66.9 | 35.3 | 0 | 0 | 998 | -4.97 | 0 | 0
BHLC002R | 2020-02-12 11:05 | 66.6 | 35.3 | 0.2 | 0 | 998 | -1.9 | 0 | 0
BHGV0044 | 2020-02-12 11:07 | 34.5 | 27.4 | 1.2 | 36.9 | 998 | -4.66 | 0 | 0
BHGV0044 | 2020-02-12 11:07 | 34.4 | 27.5 | 1.2 | 36.9 | 998 | 0.12 | 0 | 0
BHGV0004 | 2020-02-12 11:11 | 39.2 | 27.8 | 0.8 | 32.2 | 998 | -4.49 | 0 | 0
BHGV0004 | 2020-02-12 11:11 | 39.2 | 27.7 | 1.1 | 32 | 998 | -5.12 | 0 | 0
BHGV0003 | 2020-02-12 11:14 | 68.2 | 33.1 | 0.1 | 0 | 998 | -4.91 | 0 | 0
BHGV0045 | 2020-02-12 11:18 | 64.1 | 34.7 | 0.2 | 1 | 998 | -3.15 | 0 | 0
BHR00001 | 2020-02-12 11:20 | 56.6 | 29.7 | 2.2 | 11.5 | 998 | -5 | 0 | 0
BHR00001 | 2020-02-12 11:20 | 56.6 | 29.9 | 2.2 | 11.3 | 998 | -0.52 | 1 | 0
BHLC002B | 2020-02-12 11:25 | 46.9 | 31.4 | 3.3 | 18.4 | 996 | -1.32 | 0 | 0
BHLC002B | 2020-02-12 11:26 | 46.8 | 30.2 | 3.8 | 19.2 | 996 | -0.78 | 0 | 0
BHGV0026 | 2020-02-12 11:30 | 63.3 | 38.6 | 0.4 | 0 | 996 | -1.82 | 1 | 0
BHR0002B | 2020-02-12 11:32 | 41.3 | 24.8 | 0.5 | 33.4 | 996 | -9.48 | 2 | 0
BHGV000A | 2020-02-12 11:35 | 60.3 | 40.9 | 0 | 0 | 997 | -2.84 | 3 | 1
BHGV0046 | 2020-02-12 11:36 | 58.2 | 39.6 | 0 | 2.2 | 997 | -3.82 | 4 | 0
BHGV0046 | 2020-02-12 11:36 | 58.2 | 39.6 | 0 | 2.2 | 997 | -0.63 | 3 | 0
BHGV0027 | 2020-02-12 11:41 | 61.6 | 39.9 | 0 | 0 | 997 | -3.35 | 1 | 0
BHGV0025 | 2020-02-12 11:46 | 58.5 | 35 | 0 | 6.5 | 998 | -2.9 | 0 | 0
BHGV0025 | 2020-02-12 11:46 | 57.7 | 34.6 | 0 | 7.7 | 998 | -0.9 | 0 | 0
BHGV0024 | 2020-02-12 11:51 | 63.4 | 38.2 | 0.1 | 0 | 998 | -4.54 | 0 | 0
BHGV0028 | 2020-02-12 11:54 | 59.6 | 41.2 | 0.1 | 0 | 997 | -2.42 | 3 | 0
BHGV0028 | 2020-02-12 11:54 | 59.4 | 41.2 | 0.1 | 0 | 997 | -0.84 | 1 | 0
BHGV000B | 2020-02-12 11:55 | 61.3 | 37 | 0.6 | 1.1 | 997 | -3.36 | 1 | 0
BHGV0030 | 2020-02-12 11:57 | 60.9 | 39.1 | 0.5 | 0 | 997 | -3.21 | 3 | 0
BHGV0030 | 2020-02-12 11:58 | 59.6 | 39.5 | 0.3 | 0.6 | 997 | -0.17 | 3 | 0
BHGV000C | 2020-02-12 11:59 | 59.5 | 41.6 | 0 | 0 | 997 | -3.02 | 4 | 0
BHGV0029 | 2020-02-12 12:01 | 65.4 | 36.3 | 1.7 | 0 | 997 | -3.98 | 1 | 0
BHLC0005 | 2020-02-12 12:07 | 0.2 | 0.7 | 16.3 | 82.8 | 997 | -3.39 | 0 | 0
BHGV0031 | 2020-02-12 12:09 | 62.8 | 37.9 | 0.4 | 0 | 997 | -3.63 | 0 | 0
BHGV0048 | 2020-02-12 12:12 | 60.8 | 37.7 | 0.3 | 1.2 | 998 | -3.7 | 1 | 0
BHGV0023 | 2020-02-12 12:15 | 64.8 | 37.2 | 0.5 | 0 | 998 | -4.35 | 0 | 0
BHLC0006 | 2020-02-12 12:17 | 66.6 | 35.5 | 0 | 0 | 997 | -1.96 | 0 | 0
BHLC0006 | 2020-02-12 12:17 | 66.4 | 35.5 | 0 | 0 | 997 | -0.53 | 0 | 0
BHGV0022 | 2020-02-12 12:19 | 64.5 | 37.3 | 0 | 0 | 998 | 41.08 | 0 | 0
BHR0006B | 2020-02-12 12:21 | 52.2 | 33.6 | 1.6 | 12.6 | 997 | 6.11 | 5 | 0
BHR0006B | 2020-02-12 12:22 | 52 | 33.9 | 1.7 | 12.4 | 997 | -0.44 | 4 | 0
BHGV0033 | 2020-02-12 12:24 | 59.5 | 36.4 | 0.5 | 3.6 | 997 | -3.31 | 2 | 0
BHGV0032 | 2020-02-12 12:27 | 59.4 | 40.7 | 0.3 | 0 | 997 | 0.48 | 3 | 1
BHGV0049 | 2020-02-12 12:29 | 60 | 31.8 | 0.4 | 7.8 | 997 | -2.61 | 0 | 0
BHGV0049 | 2020-02-12 12:29 | 59.8 | 31.7 | 0.6 | 7.9 | 997 | 0.01 | 0 | 0
BHGW0034 | 2020-02-12 12:32 | 7 | 13.8 | 4 | 75.2 | 998 | -0.89 | 2 | 0
BHGW0034 | 2020-02-12 12:32 | 6.8 | 13.5 | 4.2 | 75.5 | 998 | 0.27 | 2 | 0
BHG010MA | 2020-02-12 12:35 | 56.5 | 34.9 | 0.6 | 8 | 998 | -5.8 | 0 | 0
BHG01MDA | 2020-02-12 12:38 | 56.7 | 35.2 | 0.6 | 7.5 | 998 | 197.85 | 1 | 0

## March 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-03-05
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.2 | 17.2 | 82.4 | 0 | 0 | 1004 | -0.39 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.1 | 17.6 | 82.2 | 0 | 0 | 1004 | -0.35 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1004 | -0.19 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.9 | 3 | 15.5 | 75.6 | 0 | 0 | 1004 | -0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.7 | 2.8 | 15.1 | 79.4 | 0 | 0 | 1004 | -1.19 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.5 | 16 | 81.4 | 0 | 0 | 1004 | 1.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.4 | 15.7 | 82.8 | 0 | 0 | 1004 | 0.23 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 0.5 | 16.9 | 82.4 | 0 | 0 | 1004 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.7 | 17.2 | 82 | 0 | 0 | 1004 | -1 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 1 | 17 | 81.9 | 0 | 0 | 1004 | -1.21 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.4 | 17.4 | 82.2 | 0 | 0 | 1004 | 0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 2 | 17 | 80.9 | 0 | 0 | 1004 | -0.55 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.6 | 16.3 | 82.1 | 0 | 0 | 1004 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1004 | 0.14 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 1.5 | 16.9 | 81.5 | 0 | 0 | 1004 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.3 | 17 | 82.6 | 0 | 0 | 1004 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.6 | 16.8 | 82.5 | 0 | 0 | 1004 | -0.05 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-03-12
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA10078
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 989 | -0.11 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.9 | 15.3 | 82.8 | 0 | 0 | 990 | -0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18 | 82 | 0 | 0 | 990 | -0.21 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.1 | 2.7 | 14.9 | 80.3 | 0 | 0 | 990 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.4 | 6.1 | 15.3 | 70.2 | 0 | 0 | 989 | -0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 0.2 | 18.2 | 81.5 | 0 | 0 | 990 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.9 | 8.6 | 87.5 | 0 | 0 | 990 | -0.13 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 990 | 0.2 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 990 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.2 | 17.4 | 82.4 | 0 | 0 | 990 | -0.16 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 18.2 | 81.6 | 0 | 0 | 990 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 15.8 | 82.8 | 0 | 0 | 990 | -0.08 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 990 | 0.17 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 17.3 | 80.8 | 0 | 0 | 990 | -0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 990 | -0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 18.5 | 81.3 | 0 | 0 | 990 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-03-18
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 17.5 | 82.3 | 0 | 0 | 1009 | -0.44 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.2 | 17.5 | 82.2 | 0 | 0 | 1009 | -0.38 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1009 | -0.2 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.6 | 2.8 | 14.5 | 77.1 | 0 | 0 | 1009 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.9 | 2.5 | 14.6 | 80 | 0 | 0 | 1009 | -1.15 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.4 | 14.6 | 82.9 | 0 | 0 | 1009 | 1.67 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.1 | 15.6 | 83.2 | 0 | 0 | 1009 | 0.48 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0.5 | 17.4 | 82 | 0 | 0 | 1009 | -0.09 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.6 | 17.4 | 81.9 | 0 | 0 | 1009 | -1.82 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 1 | 17.3 | 81.6 | 0 | 0 | 1009 | -1.75 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 1009 | -0.11 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 2.1 | 16.9 | 80.9 | 0 | 0 | 1009 | -0.87 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 15.8 | 82.8 | 0 | 0 | 1009 | -0.08 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.4 | 81.6 | 0 | 0 | 1009 | 0.16 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 1.7 | 16.4 | 81.8 | 0 | 0 | 1008 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.2 | 17.7 | 82 | 0 | 0 | 1008 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.8 | 16.5 | 82.6 | 0 | 0 | 1008 | -0.09 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-03-26
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.3 | 0.3 | 17.4 | 82 | 0 | 0 | 1002 | -0.36 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 0.2 | 17.7 | 81.9 | 0 | 0 | 1002 | -0.31 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1002 | -0.23 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.6 | 2.8 | 15.7 | 75.9 | 0 | 0 | 1002 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.5 | 2.6 | 15.4 | 79.5 | 0 | 0 | 1002 | -1.21 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.2 | 2.4 | 16.3 | 81.1 | 0 | 0 | 1002 | 1.07 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.5 | 15.9 | 82.5 | 0 | 0 | 1002 | 0.21 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.3 | 0.4 | 16.5 | 82.8 | 0 | 0 | 1002 | -0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.2 | 0.6 | 17.4 | 81.8 | 0 | 0 | 1002 | -1.23 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.2 | 1.2 | 17.2 | 81.4 | 0 | 0 | 1002 | -1.21 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0 | 0.5 | 17.6 | 81.9 | 0 | 0 | 1002 | 0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 2.1 | 17.2 | 80.5 | 0 | 0 | 1002 | -0.42 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.7 | 16.5 | 81.8 | 0 | 0 | 1002 | -0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 1002 | 0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 1.4 | 16.8 | 81.7 | 0 | 0 | 1002 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.2 | 17.2 | 82.5 | 0 | 0 | 1002 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.7 | 16.5 | 82.7 | 0 | 0 | 1002 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA12599 | MCERTS certified instrument
Date downloaded | 2020-03-18 07:49 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-03-06
Date of last factory calibration | 2019-11-23
Next service due | 2020-05-23
Date of last Gas Check | 2019-11-23
Security code | [73BAEEBB]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-03-17 09:29 | 55.6 | 34.5 | 0.9 | 9 | 1008 | 183.26 | 1 | 0
BHG01MDB | 2020-03-17 09:32 | 54.6 | 35.2 | 0.8 | 9.4 | 1008 | -17.18 | 3 | 0
BHGV0035 | 2020-03-17 09:35 | 60.8 | 37.6 | 0.5 | 1.1 | 1007 | -3.81 | 1 | 0
BHGV0035 | 2020-03-17 09:36 | 60.5 | 37.8 | 0.5 | 1.2 | 1007 | -0.18 | 1 | 0
BHGV0036 | 2020-03-17 09:37 | 29.6 | 31.6 | 0.5 | 38.3 | 1007 | -7.93 | 1 | 0
BHGV0036 | 2020-03-17 09:38 | 29.6 | 31.7 | 0.5 | 38.2 | 1007 | -0.36 | 1 | 0
BHGV0037 | 2020-03-17 09:39 | 44.8 | 27.2 | 1.7 | 26.3 | 1007 | -4.57 | 0 | 0
BHGV0037 | 2020-03-17 09:39 | 44.8 | 27.2 | 1.6 | 26.4 | 1007 | -2.75 | 0 | 0
BHM010MB | 2020-03-17 09:41 | 60.1 | 39.1 | 0.4 | 0.4 | 1007 | -7.6 | 3 | 0
BHGV0018 | 2020-03-17 09:42 | 60.6 | 41.7 | 0.1 | 0 | 1007 | -7.6 | 5 | 0
BHLC004B | 2020-03-17 09:43 | 0.8 | 3.1 | 16.7 | 79.4 | 1007 | -58.42 | 2 | 0
BHR0004B | 2020-03-17 09:45 | 1.2 | 3.3 | 10.7 | 84.8 | 1007 | 0.3 | 2 | 0
BHGV0015 | 2020-03-17 09:46 | 61.1 | 38.2 | 0.5 | 0.2 | 1007 | -8.07 | 3 | 0
BHGV0014 | 2020-03-17 09:48 | 61.6 | 38 | 0.3 | 0.1 | 1007 | -7.43 | 3 | 0
BHGV0014 | 2020-03-17 09:48 | 61.5 | 38.2 | 0.1 | 0.2 | 1007 | -2.03 | 3 | 0
BHGV0013 | 2020-03-17 09:49 | 0.9 | 6.7 | 13 | 79.4 | 1007 | -0.89 | 2 | 0
BHGV0016 | 2020-03-17 09:50 | 59.7 | 35.6 | 0.4 | 4.3 | 1007 | -7.26 | 3 | 0
BHGV0016 | 2020-03-17 09:50 | 58.7 | 35.7 | 0.2 | 5.4 | 1007 | -2.36 | 3 | 0
BHM010MA | 2020-03-17 09:52 | 59.9 | 39.3 | 0.2 | 0.6 | 1007 | -7.09 | 4 | 0
BHL000C4 | 2020-03-17 09:54 | 35.1 | 23.9 | 4.6 | 36.4 | 1007 | 0.99 | 24 | 0
BHL000C4 | 2020-03-17 09:55 | 35.1 | 23.9 | 4.6 | 36.4 | 1007 | -1.46 | 20 | 0
BHGV0017 | 2020-03-17 09:56 | 32.2 | 27.3 | 4.7 | 35.8 | 1006 | -2.09 | 21 | 0
BHGV0038 | 2020-03-17 09:57 | 0.8 | 2.3 | 17.1 | 79.8 | 1006 | -1.99 | 0 | 0
BHGV0039 | 2020-03-17 09:59 | 46.8 | 26.2 | 2.1 | 24.9 | 1006 | -8.17 | 5 | 0
BHGV0039 | 2020-03-17 09:59 | 45.9 | 26.8 | 1.9 | 25.4 | 1006 | -2.87 | 6 | 0
BHGV0011 | 2020-03-17 10:00 | 33.9 | 26.2 | 1.2 | 38.7 | 1007 | -1.7 | 0 | 0
BHGV0010 | 2020-03-17 10:02 | 57.1 | 26.7 | 0.7 | 15.5 | 1007 | -2.44 | 0 | 0
BHGV0010 | 2020-03-17 10:02 | 55.5 | 27.5 | 0.2 | 16.8 | 1007 | -3.05 | 0 | 0
BHGV0040 | 2020-03-17 10:03 | 57.9 | 32.9 | 0.8 | 8.4 | 1007 | -8.98 | 0 | 0
BHGV0040 | 2020-03-17 10:04 | 52.4 | 30.6 | 0.2 | 16.8 | 1007 | -3.19 | 0 | 0
BHLC001B | 2020-03-17 10:05 | 33.4 | 21 | 7.3 | 38.3 | 1007 | -6.43 | 1 | 0
BHLC001B | 2020-03-17 10:05 | 33.5 | 20.9 | 7.3 | 38.3 | 1007 | -2.85 | 1 | 0
BHGV0009 | 2020-03-17 10:07 | 56.4 | 31.8 | 0.6 | 11.2 | 1007 | -7.74 | 1 | 0
BHGV0009 | 2020-03-17 10:08 | 56.1 | 31.7 | 0.7 | 11.5 | 1007 | -2.43 | 1 | 0
BHGV0041 | 2020-03-17 10:10 | 65.7 | 36.6 | 0.4 | 0 | 1007 | -3.96 | 1 | 0
BHGV0041 | 2020-03-17 10:10 | 65.1 | 37.2 | 0.1 | 0 | 1007 | -3.06 | 2 | 0
BHGV0046 | 2020-03-17 10:12 | 30.6 | 24.2 | 4.7 | 40.5 | 1005 | -2.7 | 64 | 0
BHGV0046 | 2020-03-17 10:12 | 30.6 | 24.4 | 4.6 | 40.4 | 1005 | -2.93 | 57 | 0
BHGV0043 | 2020-03-17 10:15 | 51.6 | 30.3 | 0.1 | 18 | 1006 | -6.72 | 1 | 0
BHGV0043 | 2020-03-17 10:15 | 51.1 | 30.5 | 0.1 | 18.3 | 1006 | -2.66 | 1 | 0
BHGV0007 | 2020-03-17 10:20 | 57.6 | 30.7 | 0.6 | 11.1 | 1007 | -7.68 | 1 | 0
BHGV0007 | 2020-03-17 10:20 | 58.4 | 30.7 | 0.9 | 10 | 1007 | -2.81 | 1 | 0
BHGV0008 | 2020-03-17 10:22 | 15.2 | 12.1 | 10.2 | 62.5 | 1007 | -8.27 | 8 | 0
BHLC002R | 2020-03-17 10:24 | 56.5 | 32.8 | 0.5 | 10.2 | 1007 | -9.3 | 1 | 0
BHLC002R | 2020-03-17 10:24 | 56.4 | 33 | 0.4 | 10.2 | 1007 | -2.94 | 1 | 0
BHGV0044 | 2020-03-17 10:25 | 21.6 | 23.9 | 2.4 | 52.1 | 1007 | -8.08 | 1 | 0
BHGV0044 | 2020-03-17 10:26 | 21.6 | 23.8 | 2.4 | 52.2 | 1007 | -2.41 | 1 | 0
BHGV0004 | 2020-03-17 10:29 | 45.4 | 30.5 | 1.1 | 23 | 1007 | -7.88 | 0 | 0
BHGV0004 | 2020-03-17 10:29 | 44.4 | 30.9 | 0.9 | 23.8 | 1007 | -10.94 | 1 | 0
BHGV0003 | 2020-03-17 10:30 | 59.4 | 32.7 | 1.5 | 6.4 | 1007 | -7.92 | 1 | 0
BHGV0045 | 2020-03-17 10:39 | 44.2 | 25.5 | 3.3 | 27 | 1007 | -7.96 | 30 | 0
BHR00001 | 2020-03-17 10:41 | 67 | 35 | 0.4 | 0 | 1007 | -6.15 | 6 | 0
BHR00001 | 2020-03-17 10:41 | 65.1 | 35 | 0.5 | 0 | 1007 | -2.9 | 6 | 0
BHR0001B | 2020-03-17 10:43 | 58.8 | 33.3 | 0.8 | 7.1 | 1006 | 2.51 | 2 | 0
BHGV0026 | 2020-03-17 10:48 | 63 | 38.7 | 2.3 | 0 | 1005 | 0.43 | 0 | 0
BHGV0027 | 2020-03-17 10:52 | 62.2 | 40.6 | 0.3 | 0 | 1005 | 0.98 | 3 | 0
BHGV0025 | 2020-03-17 10:58 | 63.1 | 39.3 | 0.3 | 0 | 1005 | -0.26 | 1 | 0
BHGV0024 | 2020-03-17 11:01 | 63.3 | 39.9 | 0.1 | 0 | 1006 | 2.94 | 2 | 0
BHGV0023 | 2020-03-17 11:07 | 64.1 | 39 | 0.1 | 0 | 1006 | 1.78 | 1 | 0
BHGV0048 | 2020-03-17 11:10 | 65.8 | 36 | 3.5 | 0 | 1006 | 1.47 | 0 | 0
BHGV0029 | 2020-03-17 11:12 | 62.3 | 41 | 0.1 | 0 | 1005 | -3.87 | 4 | 0
BHGV0028 | 2020-03-17 11:13 | 62.8 | 38.8 | 1.4 | 0 | 1005 | -3.58 | 3 | 0
BHGV0028 | 2020-03-17 11:14 | 61.9 | 40 | 0.4 | 0 | 1005 | -2.98 | 3 | 0
BHGV000C | 2020-03-17 11:15 | 64.4 | 39.7 | 0.6 | 0 | 1005 | -1.76 | 2 | 0
BHGV000B | 2020-03-17 11:17 | 66.4 | 36.2 | 1 | 0 | 1005 | -3.03 | 1 | 2
BHGV0030 | 2020-03-17 11:19 | 64 | 38.8 | 0.7 | 0 | 1005 | -2.29 | 2 | 0
BHGV0030 | 2020-03-17 11:19 | 61.8 | 38.7 | 0.2 | 0 | 1005 | -2.58 | 3 | 0
BHGV0031 | 2020-03-17 11:20 | 64.9 | 37.6 | 0.7 | 0 | 1005 | -6.7 | 1 | 0
BHLC0005 | 2020-03-17 11:24 | 61.1 | 41.7 | 0.2 | 0 | 1005 | -0.11 | 2 | 0
BHLC0005 | 2020-03-17 11:24 | 60.2 | 41.8 | 0.1 | 0 | 1005 | -3.1 | 3 | 0
BHLC006B | 2020-03-17 11:26 | 56.8 | 37.5 | 1.1 | 4.6 | 1005 | -3.78 | 1 | 0
BHLC006B | 2020-03-17 11:27 | 56.3 | 37.6 | 1.1 | 5 | 1005 | -3.03 | 1 | 0
BHLC0006 | 2020-03-17 11:29 | 62.9 | 37.7 | 0.5 | 0 | 1005 | 2.16 | 1 | 0
BHLC0006 | 2020-03-17 11:29 | 60.4 | 37.5 | 0.7 | 1.4 | 1005 | -2.77 | 1 | 0
BHGV0022 | 2020-03-17 11:31 | 76.5 | 23.6 | 6.6 | 0 | 1005 | 42.2 | 0 | 0
BHGV0049 | 2020-03-17 11:33 | 63.3 | 32.2 | 0.6 | 3.9 | 1006 | -4.14 | 0 | 0
BHGV0049 | 2020-03-17 11:33 | 62.4 | 32.9 | 0.2 | 4.5 | 1006 | -2.64 | 0 | 0
BHGV0033 | 2020-03-17 11:34 | 61.7 | 37.1 | 0.6 | 0.6 | 1005 | -2.98 | 0 | 0
BHGV0032 | 2020-03-17 11:36 | 61.4 | 41.1 | 0.3 | 0 | 1005 | -0.55 | 2 | 0
BHGW0034 | 2020-03-17 11:37 | 33.5 | 33.3 | 1 | 32.2 | 1006 | -2.19 | 3 | 0
BHG010MA | 2020-03-17 11:41 | 55.3 | 33.7 | 1.2 | 9.8 | 1006 | -16.75 | 2 | 0
BHG01MDA | 2020-03-17 11:44 | 57.6 | 35.1 | 0.8 | 6.5 | 1006 | 185.11 | 1 | 0

## April 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-04-03
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 16.9 | 82.6 | 0 | 0 | 1013 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 1013 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.9 | 3 | 13.1 | 76 | 0 | 0 | 1014 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.9 | 1.1 | 17.8 | 80.2 | 0 | 0 | 1014 | -0.15 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.6 | 16.1 | 81.3 | 0 | 0 | 1014 | -0.12 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.2 | 16.5 | 82.3 | 0 | 0 | 1014 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.9 | 17.1 | 82 | 0 | 0 | 1014 | -0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.5 | 17.9 | 81.5 | 0 | 0 | 1014 | 0.09 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.1 | 17.4 | 81.5 | 0 | 0 | 1014 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 1.9 | 17.2 | 80.8 | 0 | 0 | 1014 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.7 | 16.6 | 81.7 | 0 | 0 | 1014 | -0.1 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1013 | 0.11 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 1.9 | 17.3 | 80.7 | 0 | 0 | 1013 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1013 | 0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.8 | 16.8 | 82.3 | 0 | 0 | 1014 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-04-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 17.2 | 82.3 | 0 | 0 | 1008 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.2 | 16.9 | 81.9 | 0 | 0 | 1008 | 0.05 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 17 | 82.8 | 0 | 0 | 1008 | -0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6 | 3.1 | 12.2 | 78.7 | 0 | 0 | 1008 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.3 | 0.6 | 17.7 | 81.4 | 0 | 0 | 1008 | -0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.9 | 15.4 | 81.7 | 0 | 0 | 1008 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 16 | 82.5 | 0 | 0 | 1009 | -0.15 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.4 | 82.3 | 0 | 0 | 1008 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 1008 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 17.7 | 81.7 | 0 | 0 | 1008 | 0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.5 | 17.1 | 81.4 | 0 | 0 | 1008 | 0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.5 | 16.8 | 81.7 | 0 | 0 | 1008 | -0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1008 | 0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.2 | 17.7 | 81.1 | 0 | 0 | 1008 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 17.1 | 82.5 | 0 | 0 | 1008 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 16.3 | 83.2 | 0 | 0 | 1008 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-04-17
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.8 | 81.9 | 0 | 0 | 1013 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 17.4 | 81.7 | 0 | 0 | 1013 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1013 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.9 | 3.1 | 12.7 | 80.3 | 0 | 0 | 1012 | -0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.4 | 0.7 | 17.5 | 81.4 | 0 | 0 | 1013 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.4 | 16.5 | 81.1 | 0 | 0 | 1012 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.1 | 17 | 81.9 | 0 | 0 | 1012 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.5 | 16 | 82.5 | 0 | 0 | 1012 | -0.12 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 16.4 | 82.3 | 0 | 0 | 1013 | 0 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 1013 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.2 | 17.1 | 81.7 | 0 | 0 | 1013 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 1013 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1012 | 0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 1012 | -0.09 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 1013 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 16.5 | 83.3 | 0 | 0 | 1013 | -0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-04-24
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 1002 | -0.07 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.7 | 16.3 | 82 | 0 | 0 | 1002 | -0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.4 | 16.5 | 83 | 0 | 0 | 1002 | -0.23 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.7 | 2.5 | 14.2 | 79.6 | 0 | 0 | 1003 | 0.09 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.4 | 0.8 | 17.3 | 81.5 | 0 | 0 | 1002 | -0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 15.9 | 81.9 | 0 | 0 | 1002 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.9 | 15.8 | 82.3 | 0 | 0 | 1003 | -0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 17 | 81.6 | 0 | 0 | 1002 | -0.2 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 16.9 | 82.5 | 0 | 0 | 1002 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 17.3 | 82 | 0 | 0 | 1002 | -0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.2 | 17.6 | 81.2 | 0 | 0 | 1002 | -0.15 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 1002 | 0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 17.8 | 82.2 | 0 | 0 | 1002 | 0.06 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.9 | 17.2 | 81.9 | 0 | 0 | 1002 | -0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 1002 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.3 | 16.9 | 82.8 | 0 | 0 | 1002 | 0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12599 | MCERTS certified instrument
Date downloaded | 2020-04-24 16:28 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-04-22
Date of last factory calibration | 2019-11-23
Next service due | 2020-05-23
Date of last Gas Check | 2019-11-23
Security code | [C9BB403D]
ID | DATE | CH4 | CO2 | O2 | BALANCE | CO | H2S | BARO | REL.PRESSURE
|  | % | % | % | % | ppm | ppm | mb | mb
BHG01MDB | 2020-04-24 08:48 | 49.4 | 31.9 | 1.7 | 17 | 1 | 0 | 1003 | 164.47
BHG010MB | 2020-04-24 09:52 | 45.4 | 31.5 | 2.2 | 20.9 | 0 | 0 | 1002 | -28.99
BHGV0035 | 2020-04-24 09:54 | 51.5 | 34.7 | 0.3 | 13.5 | 0 | 0 | 1002 | -2.82
BHGV0035 | 2020-04-24 09:55 | 51.3 | 35.2 | 0.3 | 13.2 | 0 | 0 | 1002 | -0.03
BHGV0036 | 2020-04-24 09:56 | 63 | 32.5 | 0.4 | 4.1 | 0 | 0 | 1002 | -0.59
BHGV0036 | 2020-04-24 09:56 | 62.9 | 32.8 | 0.2 | 4.1 | 0 | 0 | 1002 | -0.02
BHGV0037 | 2020-04-24 09:59 | 32.8 | 26.2 | 1.7 | 39.3 | 0 | 0 | 1003 | -3.05
BHGV0037 | 2020-04-24 10:00 | 32.9 | 26.2 | 1.7 | 39.2 | 0 | 0 | 1003 | -0.03
BHM010MB | 2020-04-24 10:01 | 60.7 | 39.4 | 0.2 | 0 | 3 | 0 | 1002 | -4.83
BHGV0018 | 2020-04-24 10:03 | 60.1 | 41.7 | 0.2 | 0 | 3 | 0 | 1002 | -4.93
BHLC004B | 2020-04-24 10:04 | 0.5 | 6.1 | 14.7 | 78.7 | 4 | 0 | 1002 | 1.54
BHR0004B | 2020-04-24 10:05 | 53.7 | 33.5 | 0.4 | 12.4 | 2 | 0 | 1002 | 2.62
BHR0004B | 2020-04-24 10:06 | 53.7 | 33.8 | 0.4 | 12.1 | 2 | 0 | 1002 | -5.03
BHGV0015 | 2020-04-24 10:07 | 60 | 39.9 | 0.2 | 0 | 3 | 0 | 1002 | -4.94
BHGV0014 | 2020-04-24 10:08 | 60.3 | 39.3 | 0.1 | 0.3 | 2 | 0 | 1002 | -3.56
BHGV0014 | 2020-04-24 10:08 | 61.3 | 40.5 | 0.1 | 0 | 2 | 0 | 1002 | -0.1
BHGV0013 | 2020-04-24 10:11 | 48.4 | 33.1 | 2.2 | 16.3 | 2 | 0 | 1002 | 0.3
BHGV0013 | 2020-04-24 10:11 | 48.2 | 33.2 | 2.3 | 16.3 | 2 | 0 | 1002 | -4.21
BHGV0016 | 2020-04-24 10:14 | 56.2 | 37.6 | 0.5 | 5.7 | 2 | 0 | 1002 | -4.49
BHGV0016 | 2020-04-24 10:14 | 56.2 | 37.6 | 0.5 | 5.7 | 2 | 0 | 1002 | 0.14
BHM010MA | 2020-04-24 10:16 | 57.4 | 40.6 | 0.4 | 1.6 | 2 | 0 | 1001 | -4.38
BHL000C4 | 2020-04-24 10:23 | 64.6 | 37.7 | 0.1 | 0 | 2 | 1 | 1001 | 0.18
BHL000C4 | 2020-04-24 10:23 | 63.6 | 38 | 0.3 | 0 | 2 | 1 | 1001 | -0.05
BHGV0017 | 2020-04-24 10:23 | 31.4 | 35.1 | 1.2 | 32.3 | 1 | 0 | 1001 | 0.29
BHGV0038 | 2020-04-24 10:28 | 26.6 | 18.8 | 7.6 | 47 | 2 | 0 | 1001 | -0.01
BHGV0038 | 2020-04-24 10:29 | 26.6 | 18.8 | 7.8 | 46.8 | 0 | 0 | 1001 | -0.72
BHGV0039 | 2020-04-24 10:32 | 53.4 | 31 | 0.7 | 14.9 | 1 | 0 | 1001 | -4.11
BHGV0039 | 2020-04-24 10:33 | 52.8 | 31.1 | 0.9 | 15.2 | 0 | 0 | 1001 | -2.53
BHGV0011 | 2020-04-24 10:35 | 33 | 23.7 | 0.3 | 43 | 0 | 0 | 1001 | -0.71
BHGV0010 | 2020-04-24 10:36 | 47.3 | 22.7 | 0.3 | 29.7 | 0 | 0 | 1001 | -2.78
BHGV0010 | 2020-04-24 10:36 | 46.4 | 24.1 | 0.2 | 29.3 | 0 | 0 | 1001 | -2.29
BHGV0040 | 2020-04-24 10:41 | 51.5 | 32 | 1 | 15.5 | 1 | 0 | 1000 | -3.63
BHGV0040 | 2020-04-24 10:41 | 51.1 | 32.1 | 1.1 | 15.7 | 1 | 0 | 1000 | -0.12
BHGV0046 | 2020-04-24 10:43 | 60.4 | 41.6 | 0.6 | 0 | 1 | 0 | 1000 | 1.95
BHGV0046 | 2020-04-24 10:44 | 60.2 | 41.6 | 0.7 | 0 | 1 | 0 | 1000 | 1.03
BHGV0041 | 2020-04-24 10:46 | 61.5 | 39.5 | 0.1 | 0 | 2 | 0 | 1000 | -3.78
BHGV0041 | 2020-04-24 10:47 | 61.3 | 39.6 | 0.5 | 0 | 1 | 0 | 1000 | -3.66
BHGV0042 | 2020-04-24 10:50 | 24.3 | 11.1 | 9.4 | 55.2 | 1 | 0 | 999 | 0.24
BHGV0043 | 2020-04-24 10:54 | 40.8 | 27.8 | 0.3 | 31.1 | 0 | 0 | 1001 | -3.89
BHGV0043 | 2020-04-24 10:54 | 40.6 | 27.9 | 0.5 | 31 | 0 | 0 | 1001 | -4.32
BHGV0007 | 2020-04-24 10:58 | 28.7 | 24 | 0.8 | 46.5 | 0 | 0 | 1001 | -3.96
BHGV0007 | 2020-04-24 10:58 | 28.8 | 24.1 | <<<< | >>>> | 0 | 0 | 1001 | -0.11
BHGV0008 | 2020-04-24 11:00 | 36.9 | 21.8 | 5.6 | 35.7 | 5 | 0 | 1001 | 28.39
BHLC002R | 2020-04-24 11:04 | 59 | 35.8 | 0.1 | 5.1 | 0 | 0 | 1001 | -4.4
BHLC002R | 2020-04-24 11:04 | 59 | 35.8 | 0.1 | 5.1 | 0 | 0 | 1001 | -5.51
BHGV0044 | 2020-04-24 11:09 | 16.3 | 17.4 | 2.9 | 63.4 | 0 | 0 | 1001 | -0.31
BHR0001B | 2020-04-24 11:13 | 58.3 | 28.8 | 2.4 | 10.5 | 1 | 0 | 999 | -1.45
BHGV0045 | 2020-04-24 11:17 | 59.2 | 34.7 | 0.9 | 5.2 | 0 | 0 | 999 | -2.65
BHLC002B | 2020-04-24 11:22 | 57.4 | 34.3 | 1.6 | 6.7 | 2 | 0 | 999 | -0.89
BHLC002B | 2020-04-24 11:22 | 56.9 | 35.1 | 1.7 | 6.3 | 1 | 0 | 999 | -0.04
BHGV0026 | 2020-04-24 11:26 | 61.5 | 40.2 | 0.4 | 0 | 1 | 0 | 999 | 2.36
BHR0002B | 2020-04-24 11:29 | 0.3 | 9.1 | 11.8 | 78.8 | 15 | 0 | 998 | 53.95
BHGV0027 | 2020-04-24 11:31 | 61.1 | 40.5 | 0.1 | 0 | 1 | 0 | 998 | 2.33
BHGV0025 | 2020-04-24 11:38 | 60.7 | 41.4 | 0 | 0 | 2 | 0 | 998 | 1.72
BHGV0024 | 2020-04-24 11:40 | 65.4 | 36.9 | 0.3 | 0 | 1 | 0 | 999 | 2.32
BHGV0048 | 2020-04-24 11:41 | 63.6 | 38.7 | 0.2 | 0 | 1 | 0 | 999 | 1.25
BHGV0028 | 2020-04-24 11:44 | 60.3 | 41.8 | 0 | 0 | 1 | 0 | 998 | 2.14
BHGV0029 | 2020-04-24 11:45 | 62.2 | 39.9 | 0.1 | 0 | 2 | 0 | 998 | 1.45
BHGV000C | 2020-04-24 11:47 | 61.5 | 40.8 | 0.1 | 0 | 2 | 2 | 998 | 2.74
BHGV0031 | 2020-04-24 11:50 | 63.9 | 37.6 | 0.2 | 0 | 2 | 0 | 998 | -3.08
BHLC0005 | 2020-04-24 11:52 | 66.4 | 35.6 | 0.4 | 0 | 2 | 0 | 998 | 0.04
BHLC0005 | 2020-04-24 11:52 | 67.8 | 33.4 | 0.2 | 0 | 2 | 0 | 998 | 0.1
BHR0006B | 2020-04-24 11:54 | 58.1 | 35.2 | 1.1 | 5.6 | 1 | 0 | 998 | -2.83
BHR0006B | 2020-04-24 11:54 | 57 | 36.4 | 1.2 | 5.4 | 1 | 0 | 998 | 0.12
BHGV0032 | 2020-04-24 11:58 | 67.7 | 34.9 | 0.5 | 0 | 2 | 0 | 998 | 1.42
BHLC0003 | 2020-04-24 11:59 | 54.6 | 36.8 | 0.2 | 8.4 | 1 | 0 | 998 | -2.83
BHGV0049 | 2020-04-24 12:01 | 48.9 | 30.3 | 0.2 | 20.6 | 1 | 0 | 998 | -3.49
BHGV0049 | 2020-04-24 12:02 | 48.6 | 30.7 | 0.2 | 20.5 | 1 | 0 | 998 | 0.18
BHG010MA | 2020-04-24 12:05 | 50.8 | 31.9 | 1.9 | 15.4 | 2 | 0 | 999 | -20.18
BHG01MDA | 2020-04-24 12:12 | 51.6 | 32.1 | 1.8 | 14.5 | 2 | 0 | 999 | 179.9

## May 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-05-01
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.9 | 17.1 | 82 | 0 | 0 | 1005 | 0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2 | 16.6 | 81.4 | 0 | 0 | 1005 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.1 | 17.9 | 81 | 0 | 0 | 1004 | 0.09 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.3 | 18.2 | 80.5 | 0 | 0 | 1005 | 0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 16.2 | 83.4 | 0 | 0 | 1004 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4 | 2.9 | 13 | 80.1 | 0 | 0 | 1004 | 0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.3 | 0.5 | 16.6 | 82.6 | 0 | 0 | 1004 | 0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.9 | 15.5 | 82.6 | 0 | 0 | 1004 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.4 | 16.2 | 81.4 | 0 | 0 | 1004 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.9 | 16.9 | 81.2 | 0 | 0 | 1004 | -0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.8 | 16.2 | 83 | 0 | 0 | 1004 | -0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.1 | 16.6 | 82.3 | 0 | 0 | 1004 | -0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.9 | 17.1 | 81 | 0 | 0 | 1004 | -0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 1004 | 0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.3 | 18.7 | 79 | 0 | 0 | 1004 | -0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.7 | 16.9 | 82.4 | 0 | 0 | 1005 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 17.1 | 82.4 | 0 | 0 | 1004 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.6 | 16.5 | 82.9 | 0 | 0 | 1005 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-05-07
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 15.9 | 83.9 | 0 | 0 | 1009 | -0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.9 | 15.2 | 83.9 | 0 | 0 | 1010 | 1.06 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.1 | 16 | 83.9 | 0 | 0 | 1012 | -0.16 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.9 | 3 | 11.8 | 77.3 | 0 | 0 | 1010 | -0.95 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.8 | 5.2 | 14 | 72 | 0 | 0 | 1010 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 3.5 | 10.5 | 86 | 0 | 0 | 1010 | 1.45 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.4 | 16.2 | 81.4 | 0 | 0 | 1010 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.1 | 16 | 83.9 | 0 | 0 | 1010 | 0.07 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 16.1 | 83.7 | 0 | 0 | 1010 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16 | 83.8 | 0 | 0 | 1009 | 0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 15.8 | 84.1 | 0 | 0 | 1009 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 5.4 | 5.8 | 88.6 | 0 | 0 | 1009 | 0.18 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 6.5 | 11.8 | 81.7 | 0 | 0 | 1009 | -0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 15.8 | 84.1 | 0 | 0 | 1009 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.7 | 14.6 | 82.7 | 0 | 0 | 1009 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-05-14
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.7 | 16.6 | 82.7 | 0 | 0 | 1011 | -0.17 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.9 | 16.1 | 82 | 0 | 0 | 1010 | -0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.9 | 18.2 | 80.9 | 0 | 0 | 1011 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 1.4 | 17.4 | 81 | 0 | 0 | 1010 | -0.48 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 | [9 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Blocked | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.4 | 3.1 | 13.9 | 78.6 | 0 | 0 | 1010 | 0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 1.7 | 1.1 | 16.1 | 81.1 | 0 | 0 | 1010 | -0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Blocked | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.4 | 13.9 | 83.7 | 0 | 0 | 1010 | -0.21 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | Blocked | [7 empty] | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 16.5 | 83.1 | 0 | 0 | 1010 | -0.16 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 16.7 | 82.9 | 0 | 0 | 1010 | 0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.9 | 14.9 | 84.2 | 0 | 0 | 1010 | -0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.3 | 16.4 | 82.3 | 0 | 0 | 1010 | -0.13 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 3.9 | 11.1 | 84.9 | 0 | 0 | 1010 | -0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.6 | 13.9 | 83.5 | 0 | 0 | 1010 | -0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Flooded | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.9 | 16.1 | 81 | 0 | 0 | 1010 | -0.19 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 16.6 | 82.8 | 0 | 0 | 1010 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.9 | 15.4 | 82.7 | 0 | 0 | 1010 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-05-22
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.2 | 0.1 | 17 | 82.7 | 0 | 0 | 993 | -0.15 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.2 | 0.1 | 17.1 | 82.6 | 0 | 0 | 993 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0.1 | 0.8 | 16.4 | 82.7 | 0 | 0 | 993 | -0.77 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0.1 | 0.2 | 17 | 82.7 | 0 | 0 | 993 | 0.2 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 0.6 | 16.7 | 82.6 | 0 | 0 | 993 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.2 | 16.9 | 82.8 | 0 | 0 | 992 | 0.16 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.2 | 2.9 | 14.5 | 80.4 | 0 | 0 | 992 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.5 | 4.1 | 15.4 | 78 | 0 | 0 | 992 | -0.2 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.2 | 1.1 | 16.8 | 81.9 | 0 | 0 | 992 | -0.14 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 3.8 | 7.3 | 88.8 | 0 | 0 | 992 | 0.15 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.1 | 10.7 | 88.1 | 0 | 0 | 992 | -0.22 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.1 | 0 | 16.9 | 83 | 0 | 0 | 991 | -0.08 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.3 | 16.7 | 82.9 | 0 | 0 | 991 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 16.7 | 83 | 0 | 0 | 836 | -0.13 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 16.7 | 83 | 0 | 0 | 991 | 0 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.3 | 14.9 | 83.7 | 0 | 0 | 991 | 0.43 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.8 | 14.8 | 83.3 | 0 | 0 | 991 | 0.1 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 4.3 | 14.5 | 81.1 | 0 | 0 | 992 | 3.31 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 1.6 | 14.6 | 83.7 | 0 | 0 | 991 | -0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.2 | 17 | 82.7 | 0 | 0 | 992 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.7 | 16.4 | 82.8 | 0 | 0 | 992 | -0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-05-27
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 16.7 | 83.1 | 0 | 0 | 1030 | 0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0.2 | 16.5 | 83.2 | 0 | 0 | 1030 | 0.05 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.1 | 16.1 | 82.8 | 0 | 0 | 1031 | -0.14 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 16.9 | 82.6 | 0 | 0 | 1030 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 1030 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.4 | 17.2 | 82.4 | 0 | 0 | 1030 | 0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.9 | 3.1 | 12.9 | 80.1 | 0 | 0 | 1030 | 0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 5.1 | 4.5 | 11.7 | 78.7 | 0 | 0 | 1031 | -0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.3 | 82.3 | 0 | 0 | 1030 | 0.07 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 3.4 | 7.2 | 89.4 | 0 | 0 | 1030 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.5 | 11.2 | 87.3 | 0 | 0 | 1030 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1030 | 0.09 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 17.1 | 82.5 | 0 | 0 | 1030 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16.9 | 82.9 | 0 | 0 | 1030 | 0.05 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 16.4 | 83.3 | 0 | 0 | 1030 | -0.12 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 14.8 | 84.1 | 0 | 0 | 1030 | -0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 1.7 | 14.4 | 83.9 | 0 | 0 | 1030 | -0.09 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.9 | 13.9 | 82.2 | 0 | 0 | 1030 | 0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 14.9 | 83.2 | 0 | 0 | 1030 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 16.4 | 83.3 | 0 | 0 | 1030 | 0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 16.7 | 82.8 | 0 | 0 | 1030 | 0.21 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12599 | MCERTS certified instrument
Date downloaded | 2020-05-22 11:08 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-04-22
Date of last factory calibration | 2019-11-23
Next service due | 2020-05-23
Date of last Gas Check | 2019-11-23
Security code | [0F017127]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-05-22 08:26 | 54.2 | 35.9 | 1.2 | 8.7 | 994 | 148.6 | 0 | 0
BHG010MB | 2020-05-22 09:08 | 50.7 | 34.1 | 1.9 | 13.3 | 993 | -16.64 | 1 | 0
BHGV0035 | 2020-05-22 09:20 | 56.8 | 37.6 | 1.1 | 4.5 | 993 | -1.67 | 0 | 0
BHGV0035 | 2020-05-22 09:20 | 56.5 | 37.6 | 1.9 | 4 | 993 | 0.06 | 0 | 0
BHGV0036 | 2020-05-22 09:21 | 39.1 | 27.2 | 1 | 32.7 | 993 | -2.18 | 0 | 0
BHGV0036 | 2020-05-22 09:22 | 39 | 27.2 | 0.9 | 32.9 | 993 | -0.02 | 0 | 0
BHGV0037 | 2020-05-22 09:23 | 65.4 | 31.1 | 1 | 2.5 | 993 | 0.51 | 0 | 0
BHGV0037 | 2020-05-22 09:23 | 65.2 | 31.3 | 1 | 2.5 | 993 | -0.46 | 0 | 0
BHM010MB | 2020-05-22 09:25 | 55.7 | 38.8 | 1.1 | 4.4 | 993 | -2.12 | 1 | 0
BHGV0018 | 2020-05-22 09:27 | 54.7 | 40.8 | 1.2 | 3.3 | 993 | -2.6 | 2 | 0
BHLC004B | 2020-05-22 09:31 | 1.5 | 5.2 | 13.8 | 79.5 | 993 | 0 | 0 | 0
BHR0004B | 2020-05-22 09:33 | 51.1 | 32.8 | 1.2 | 14.9 | 993 | 2.76 | 1 | 0
BHR0004B | 2020-05-22 09:33 | 51.6 | 33.3 | 1.3 | 13.8 | 993 | -0.28 | 1 | 0
BHGV0015 | 2020-05-22 09:37 | 56.6 | 37.2 | 1.5 | 4.7 | 993 | -1.76 | 0 | 0
BHGV0014 | 2020-05-22 09:38 | 57 | 37.2 | 1.2 | 4.6 | 992 | -2.67 | 1 | 0
BHGV0014 | 2020-05-22 09:38 | 56.6 | 37.5 | 1.1 | 4.8 | 992 | -0.15 | 1 | 0
BHGV0013 | 2020-05-22 09:40 | 44.5 | 28.4 | 4.3 | 22.8 | 993 | -0.17 | 0 | 0
BHGV0013 | 2020-05-22 09:40 | 46.1 | 29.7 | 3.7 | 20.5 | 993 | -0.06 | 0 | 0
BHGV0016 | 2020-05-22 09:42 | 56.8 | 37.1 | 0.9 | 5.2 | 993 | -2.59 | 1 | 0
BHGV0016 | 2020-05-22 09:42 | 56.7 | 37.4 | 1 | 4.9 | 993 | -0.41 | 0 | 0
BHM010MA | 2020-05-22 09:46 | 55.9 | 38.7 | 1.1 | 4.3 | 992 | -2.14 | 2 | 0
BHL000C4 | 2020-05-22 09:48 | 61.2 | 37.8 | 0.8 | 0.2 | 992 | 0 | 0 | 20
BHL000C4 | 2020-05-22 09:49 | 61.2 | 37.8 | 0.8 | 0.2 | 992 | -0.16 | 0 | 17
BHGV0017 | 2020-05-22 09:53 | 61.3 | 38.9 | 0.5 | 0 | 992 | -2.34 | 0 | 2
BHGV0017 | 2020-05-22 09:53 | 60.3 | 38.6 | 0.7 | 0.4 | 992 | 0.05 | 10 | 1
BHGV0038 | 2020-05-22 09:55 | 63.1 | 36 | 0.8 | 0.1 | 992 | 0.42 | 0 | 0
BHGV0038 | 2020-05-22 09:56 | 63 | 36 | 0.8 | 0.2 | 992 | -1.41 | 0 | 0
BHGV0039 | 2020-05-22 09:58 | 50.8 | 31 | 1.1 | 17.1 | 992 | -2.18 | 0 | 0
BHGV0011 | 2020-05-22 10:01 | 37.6 | 29.4 | 0.3 | 32.7 | 993 | 1.07 | 0 | 0
BHGV0010 | 2020-05-22 10:06 | 64.6 | 31 | 0.6 | 3.8 | 993 | 0.9 | 0 | 0
BHGV0010 | 2020-05-22 10:06 | 64.6 | 31 | 0.6 | 3.8 | 993 | -0.11 | 0 | 0
BHGV0040 | 2020-05-22 10:08 | 53.1 | 32.3 | 0.5 | 14.1 | 992 | -1.59 | 0 | 0
BHGV0041 | 2020-05-22 10:10 | 64.3 | 34.2 | 0.9 | 0.6 | 991 | -1.98 | 0 | 0
BHGV0046 | 2020-05-22 10:12 | 59.2 | 41.3 | 0.3 | 0 | 991 | 0.61 | 1 | 0
BHGV0046 | 2020-05-22 10:12 | 59.1 | 41.5 | 0.4 | 0 | 991 | 0 | 2 | 0
BHGV0043 | 2020-05-22 10:14 | 65.3 | 35.6 | 0.4 | 0 | 992 | -0.28 | 0 | 0
BHR0001B | 2020-05-22 10:16 | 61.3 | 31 | 1.7 | 6 | 992 | -1.59 | 0 | 0
BHGV0045 | 2020-05-22 10:18 | 57.3 | 34.6 | 0.3 | 7.8 | 991 | -2.16 | 0 | 0
BHLC002B | 2020-05-22 10:25 | 63.7 | 37.2 | 0.6 | 0 | 990 | 0.08 | 0 | 0
BHLC002B | 2020-05-22 10:25 | 61.5 | 38 | 0.8 | 0 | 990 | -0.1 | 0 | 0
BHR0002B | 2020-05-22 10:27 | 0.4 | 8.6 | 11.1 | 79.9 | 991 | 37.39 | 12 | 0
BHGV0026 | 2020-05-22 10:29 | 61 | 38.3 | 0.6 | 0.1 | 991 | 0.61 | 0 | 0
BHGV0027 | 2020-05-22 10:31 | 61.9 | 38 | 0.7 | 0 | 991 | -1.86 | 1 | 2
BHGV0028 | 2020-05-22 10:34 | 59.1 | 39.2 | 0.7 | 1 | 991 | -1.89 | 1 | 0
BHGV0029 | 2020-05-22 10:39 | 57.2 | 37.7 | 1.6 | 3.5 | 991 | -1.82 | 0 | 0
BHGV000C | 2020-05-22 10:41 | 57 | 39.5 | 1.1 | 2.4 | 990 | -0.36 | 2 | 0
BHGV0031 | 2020-05-22 10:43 | 57.6 | 38.9 | 0.8 | 2.7 | 991 | -1.78 | 1 | 0
BHLC0005 | 2020-05-22 10:46 | 57.5 | 41.9 | 0.5 | 0.1 | 990 | -0.02 | 0 | 0
BHLC0005 | 2020-05-22 10:46 | 57.5 | 41.9 | 0.8 | 0 | 990 | -0.44 | 0 | 0
BHR0006B | 2020-05-22 10:48 | 54.8 | 39.8 | 1.3 | 4.1 | 991 | -1.37 | 0 | 0
BHGV0033 | 2020-05-22 10:51 | 56.6 | 35.6 | 0.8 | 7 | 991 | -1.26 | 0 | 0
BHGV0049 | 2020-05-22 10:52 | 54.9 | 31.7 | 0.8 | 12.6 | 991 | -1.49 | 0 | 0
BHGV0049 | 2020-05-22 10:52 | 54.2 | 32.1 | 0.8 | 12.9 | 991 | 0.39 | 0 | 0
BHGW0034 | 2020-05-22 10:54 | 61.7 | 25.5 | 0.6 | 12.2 | 992 | 0.22 | 0 | 0
BHGW0034 | 2020-05-22 10:55 | 61.8 | 25.3 | 0.6 | 12.3 | 992 | -0.03 | 0 | 0
BHG010MA | 2020-05-22 10:59 | 50.5 | 34.3 | 2.1 | 13.1 | 992 | -15.36 | 0 | 0
BHG01MDA | 2020-05-22 11:02 | 54.8 | 36.2 | 1.2 | 7.8 | 992 | 154.6 | 0 | 0

## June 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-06-02
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.4 | 17.1 | 82.4 | 0 | 0 | 1005 | 0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0.5 | 17 | 82.4 | 0 | 0 | 1005 | -0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.8 | 16.4 | 81.8 | 0 | 0 | 1005 | 0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.9 | 16.2 | 82.9 | 0 | 0 | 1005 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.8 | 16.4 | 82.8 | 0 | 0 | 1006 | 0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.7 | 17 | 82.3 | 0 | 0 | 1005 | 0.09 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.1 | 3.2 | 11.2 | 82.5 | 0 | 0 | 1006 | 0.34 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.1 | 4 | 9.6 | 82.3 | 0 | 0 | 1005 | 0.2 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 16.8 | 82.1 | 0 | 0 | 1005 | 0.13 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 4 | 7.9 | 88 | 0 | 0 | 1005 | 0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.9 | 10.4 | 87.6 | 0 | 0 | 1006 | 0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 16.9 | 82.9 | 0 | 0 | 1005 | -0.23 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 1007 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 15.9 | 83.7 | 0 | 0 | 1005 | -0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 | [9 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 16 | 83.6 | 0 | 0 | 1005 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.2 | 14.1 | 84.6 | 0 | 0 | 1006 | -0.16 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 2.4 | 14.8 | 82.8 | 0 | 0 | 1005 | 0.16 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 4.2 | 13.3 | 82.5 | 0 | 0 | 1005 | 0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 2.5 | 15.3 | 82.1 | 0 | 0 | 1005 | -0.15 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 17 | 82.5 | 0 | 0 | 1006 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.1 | 16.4 | 82.5 | 0 | 0 | 1005 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-06-12
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.7 | 82 | 0 | 0 | 1002 | 0.51 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.5 | 16.7 | 80.8 | 0 | 0 | 1002 | 0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.6 | 17.3 | 81.1 | 0 | 0 | 1002 | 0.41 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.1 | 17.9 | 82 | 0 | 0 | 1002 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.9 | 17.5 | 81.6 | 0 | 0 | 1002 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 1001 | 0.1 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.3 | 3.5 | 11 | 82.2 | 0 | 0 | 1001 | 0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.2 | 3.8 | 9.7 | 82.2 | 0 | 0 | 1001 | 0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17 | 81.8 | 0 | 0 | 1001 | 0.11 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 5.1 | 12.9 | 82 | 0 | 0 | 1001 | 0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5.2 | 13.3 | 81.5 | 0 | 0 | 1001 | 0.23 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 2.9 | 16.7 | 80.4 | 0 | 0 | 1001 | 0.05 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.9 | 82 | 0 | 0 | 1000 | 0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 17.6 | 82 | 0 | 0 | 1000 | 0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.9 | 82 | 0 | 0 | 1000 | 0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 999 | 0.12 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.7 | 16.9 | 82.4 | 0 | 0 | 1000 | 0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.2 | 14 | 82.7 | 0 | 0 | 1000 | 0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.4 | 15.7 | 79.9 | 0 | 0 | 1000 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 1000 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 17 | 81.3 | 0 | 0 | 1000 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-06-16
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 16 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.7 | 17.3 | 82 | 0 | 0 | 998 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 998 | 0.16 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.3 | 16.2 | 82.5 | 0 | 0 | 998 | -0.08 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 16.7 | 82.6 | 0 | 0 | 998 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 17.1 | 82.5 | 0 | 0 | 998 | 0.17 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.5 | 16.5 | 83 | 0 | 0 | 998 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.5 | 3.1 | 10.4 | 83 | 0 | 0 | 997 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.5 | 2.8 | 13.5 | 81.2 | 0 | 0 | 997 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.8 | 17.3 | 81.9 | 0 | 0 | 998 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 3.3 | 11.2 | 85.5 | 0 | 0 | 998 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.9 | 15.5 | 83.6 | 0 | 0 | 998 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 998 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 16.9 | 82.7 | 0 | 0 | 998 | 0.08 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17 | 82.8 | 0 | 0 | 997 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 16.7 | 82.9 | 0 | 0 | 998 | -0.13 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1 | 14.7 | 84.3 | 0 | 0 | 998 | -0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.7 | 16.9 | 82.4 | 0 | 0 | 998 | -0.08 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.5 | 14.6 | 81.9 | 0 | 0 | 998 | -0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 15.2 | 82.9 | 0 | 0 | 998 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 16.3 | 83.1 | 0 | 0 | 998 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.9 | 17 | 82.1 | 0 | 0 | 998 | -0.19 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-06-25
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.9 | 81.8 | 0 | 0 | 1001 | 0.26 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.7 | 16.4 | 80.9 | 0 | 0 | 1002 | 0.61 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 3.6 | 15.5 | 80.9 | 0 | 0 | 1003 | 1.41 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0 | 18.1 | 81.9 | 0 | 0 | 1003 | 0.27 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.1 | 17.5 | 814 | 0 | 0 | 1003 | 0.27 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0 | 18.1 | 81.9 | 0 | 0 | 1002 | 0.27 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 21.1 | 2.8 | 15.3 | 60.8 | 1 | 0 | 1001 | 0.28 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17 | 9.8 | 13.2 | 60 | 1 | 0 | 1002 | 0.24 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.6 | 17.2 | 82.2 | 0 | 0 | 1002 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.9 | 16.5 | 82.6 | 1 | 0 | 1002 | 0.33 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 15.2 | 84 | 0 | 0 | 1002 | 0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 17.9 | 81.9 | 1 | 0 | 1002 | 0.36 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 18 | 82 | 1 | 0 | 1001 | -0.22 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 1001 | -0.63 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 18 | 81.9 | 0 | 0 | 1001 | 0.28 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 3.7 | 11 | 85.2 | 0 | 0 | 1001 | 0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.6 | 16.7 | 82.7 | 0 | 0 | 1001 | -0.05 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 3.6 | 14.5 | 81.9 | 0 | 0 | 1001 | -0.1 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5 | 12.5 | 82.5 | 0 | 0 | 1001 | 0.28 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1001 | -0.6 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 16 | 81.9 | 0 | 0 | 1001 | 0.27 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA10292 | MCERTS certified instrument
Date downloaded | 2020-06-16 18:42 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-06-04
Date of last factory calibration | 2020-05-06
Next service due | 2020-11-06
Date of last Gas Check | N/A
Security code | [0EFB5FB9]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-06-16 09:25 | 45.3 | 32.9 | 2.4 | 19.4 | 999 | 151.46 | 2 | 0
BHG010MB | 2020-06-16 09:28 | 45.4 | 32.6 | 2.5 | 19.5 | 999 | -6.07 | 2 | 0
BHGV0035 | 2020-06-16 09:31 | 52.8 | 39.2 | 0.2 | 7.8 | 999 | -3.39 | 1 | 0
BHGV0035 | 2020-06-16 09:31 | 52.5 | 39.2 | 0.3 | 8 | 999 | -0.04 | 1 | 0
BHGV0036 | 2020-06-16 09:33 | 20.1 | 25.9 | 1.4 | 52.6 | 999 | -3.24 | 1 | 0
BHGV0036 | 2020-06-16 09:34 | 20.1 | 25.8 | 1.6 | 52.5 | 999 | 0.08 | 1 | 0
BHGV0037 | 2020-06-16 09:35 | 32.6 | 25.6 | 1.5 | 40.3 | 1000 | -2.07 | 1 | 0
BHGV0037 | 2020-06-16 09:35 | 32.9 | 26.5 | 1.5 | 39.1 | 1000 | 0.09 | 1 | 0
BHM010MB | 2020-06-16 09:37 | 57.1 | 42.7 | 0.3 | 0 | 999 | -4.02 | 2 | 0
BHGV0018 | 2020-06-16 09:41 | 57.7 | 44.8 | 0.4 | 0 | 999 | -3.97 | 0 | 0
BHLC004B | 2020-06-16 09:42 | 0.5 | 9.8 | 14.9 | 74.8 | 999 | 0.3 | 4 | 0
BHR0004B | 2020-06-16 09:45 | 55.5 | 41.7 | 0 | 2.8 | 999 | -3.99 | 1 | 0
BHR0004B | 2020-06-16 09:45 | 55.5 | 41.7 | 0 | 2.8 | 999 | 0.02 | 1 | 0
BHGV0015 | 2020-06-16 09:47 | 58.5 | 44.2 | 0.1 | 0 | 999 | -3.86 | 1 | 0
BHGV0014 | 2020-06-16 09:48 | 55.5 | 42 | 0 | 2.5 | 999 | -3.8 | 0 | 0
BHGV0013 | 2020-06-16 09:51 | 22.5 | 17.1 | 8.6 | 51.8 | 999 | 0.27 | 0 | 0
BHGV0016 | 2020-06-16 09:53 | 57.1 | 40.2 | 0 | 2.7 | 999 | -3.92 | 2 | 0
BHGV0016 | 2020-06-16 09:53 | 55.6 | 40.4 | 0.2 | 3.8 | 999 | 0.04 | 1 | 0
BHM010MA | 2020-06-16 09:54 | 60.5 | 39.9 | 0.1 | 0 | 999 | -4.06 | 2 | 0
BHGV0038 | 2020-06-16 09:56 | 43.7 | 26.8 | 3.7 | 25.8 | 999 | -2.73 | 1 | 0
BHGV0039 | 2020-06-16 09:58 | 49.1 | 32.2 | 0 | 18.7 | 999 | -3.91 | 1 | 0
BHGV0046 | 2020-06-16 10:05 | 59.2 | 43.9 | 0 | 0 | 998 | -2.14 | 1 | 0
BHGV0046 | 2020-06-16 10:05 | 59.1 | 44 | 0 | 0 | 998 | -0.06 | 1 | 0
BHGV0045 | 2020-06-16 10:14 | 56.8 | 35.5 | 0.6 | 7.1 | 998 | -3.64 | 0 | 0
BHGV0047 | 2020-06-16 10:18 | 36.6 | 32.9 | 0.3 | 30.2 | 998 | -0.31 | 0 | 0
BHGV0027 | 2020-06-16 10:19 | 60.4 | 42.2 | 0 | 0 | 998 | -3.55 | 2 | 0
BHGV0026 | 2020-06-16 10:21 | 60.4 | 40.5 | 0.5 | 0 | 998 | -4.21 | 1 | 0
BHLC002B | 2020-06-16 10:26 | 50 | 34.9 | 2.6 | 12.5 | 998 | -1.65 | 1 | 0
BHR0002B | 2020-06-16 10:29 | 0.4 | 11.6 | 10.8 | 77.2 | 998 | 37.16 | 11 | 0
BHGV000A | 2020-06-16 10:31 | 59.4 | 43.2 | 0.2 | 0 | 998 | -2.78 | 2 | 0
BHGV0028 | 2020-06-16 10:34 | 59.2 | 41.7 | 0 | 0 | 997 | -3.4 | 1 | 0
BHGV0029 | 2020-06-16 10:37 | 57.3 | 37.8 | 0 | 4.9 | 997 | -3.7 | 1 | 0
BHGV000C | 2020-06-16 10:40 | 57.9 | 44.7 | 0.8 | 0 | 997 | -1.86 | 1 | 0
BHGV0031 | 2020-06-16 10:44 | 59.4 | 39.5 | 0.1 | 1 | 997 | -2.86 | 0 | 0
BHLC0005 | 2020-06-16 10:47 | 11 | 7.3 | 14.1 | 67.6 | 997 | 0.15 | 0 | 0
BHLC0005 | 2020-06-16 10:47 | 11 | 7.5 | 14.1 | 67.4 | 997 | 0 | 0 | 0
BHLC006B | 2020-06-16 10:55 | 54.4 | 41.7 | 0.9 | 3 | 998 | -2.65 | 1 | 0
BHLC0006 | 2020-06-16 10:57 | 28.8 | 28.5 | 6.3 | 36.4 | 997 | 0.51 | 1 | 0
BHLC0006 | 2020-06-16 10:57 | 28.6 | 29.4 | 6.2 | 35.8 | 997 | -0.02 | 1 | 0
BHGV0033 | 2020-06-16 10:58 | 50.3 | 36.3 | 0.6 | 12.8 | 997 | -2.96 | 1 | 0
BHGV0049 | 2020-06-16 11:00 | 45.8 | 32.1 | 0.1 | 22 | 998 | -2.91 | 0 | 0
BHGW0034 | 2020-06-16 11:01 | 2.3 | 13.3 | 14 | 70.4 | 998 | 0.08 | 0 | 0
BHG010MA | 2020-06-16 11:04 | 52 | 32.1 | 1.8 | 14.1 | 998 | -5.64 | 1 | 0
BHG01MDA | 2020-06-16 11:06 | 50.3 | 35.3 | 1.6 | 12.8 | 998 | 151.8 | 1 | 0

## July 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-07-03
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.3 | 16.3 | 82.4 | 0 | 0 | 993 | -0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 17.2 | 82.4 | 0 | 0 | 993 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.8 | 15.9 | 82.3 | 1 | 0 | 993 | 0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 16.9 | 82.9 | 0 | 0 | 992 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 993 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 993 | 0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.2 | 3 | 11.2 | 77.6 | 1 | 0 | 993 | -0.09 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.1 | 2.2 | 7.3 | 78.4 | 1 | 0 | 993 | -0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.1 | 16.6 | 82.2 | 0 | 0 | 992 | 0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.5 | 14.8 | 82.7 | 0 | 0 | 993 | -0.13 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 14.9 | 83.8 | 0 | 0 | 992 | -0.17 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 993 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 992 | 0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 16.4 | 83 | 0 | 0 | 992 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.4 | 82.4 | 0 | 0 | 993 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.3 | 15.1 | 83.6 | 0 | 0 | 992 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 992 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.9 | 15.7 | 81.3 | 0 | 0 | 992 | 0.15 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.5 | 15 | 83.5 | 0 | 0 | 993 | -0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.8 | 16.7 | 82.5 | 0 | 0 | 993 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 17.9 | 81.6 | 0 | 0 | 993 | -0.23 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-07-09
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1 | 16.9 | 82.1 | 0 | 0 | 996 | -0.17 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 996 | -0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.6 | 15.7 | 81.7 | 0 | 0 | 996 | -0.04 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 995 | -0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 996 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.6 | 17 | 82.4 | 0 | 0 | 996 | 0.07 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.9 | 2.7 | 12.7 | 77.7 | 0 | 0 | 996 | -0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.7 | 1.9 | 8.2 | 79.2 | 1 | 0 | 995 | -0.15 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.9 | 81.7 | 0 | 0 | 995 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 15.4 | 82.4 | 0 | 0 | 995 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.7 | 13.8 | 84.5 | 0 | 0 | 995 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.4 | 17.1 | 82.5 | 0 | 0 | 996 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 994 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.9 | 15.7 | 83.4 | 0 | 0 | 995 | 0.3 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 16.9 | 82.7 | 0 | 0 | 995 | -0.14 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.7 | 16.2 | 82.1 | 0 | 0 | 994 | -0.19 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 994 | -0.06 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.2 | 16.7 | 81.1 | 0 | 0 | 994 | -0.07 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.1 | 16.3 | 82.6 | 0 | 0 | 996 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 17.4 | 82.1 | 0 | 0 | 996 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 996 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-07-16
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.6 | 17.4 | 81.8 | 0 | 0 | 1003 | 0.17 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 17.4 | 81.8 | 0 | 0 | 1004 | 0.1 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 3.2 | 15.5 | 81.3 | 0 | 0 | 1004 | 0.13 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0 | 18.2 | 81.7 | 0 | 0 | 1004 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.1 | 17.5 | 81.4 | 0 | 0 | 1005 | 0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.1 | 81.6 | 0 | 0 | 1005 | 0.12 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.4 | 3.2 | 13.6 | 69.8 | 0 | 0 | 1005 | 0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.8 | 5.5 | 15.5 | 68.2 | 0 | 0 | 1005 | 0.12 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 16.8 | 81.8 | 0 | 0 | 1005 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.8 | 18.1 | 81.1 | 0 | 0 | 1006 | 0.13 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.1 | 17 | 82.9 | 0 | 0 | 1006 | 0.31 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 1005 | -0.13 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1005 | 0.1 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 1005 | 0.1 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1004 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.7 | 12.4 | 84.9 | 0 | 0 | 1004 | 0 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 1004 | -0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1004 | 0.09 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 12.5 | 82.9 | 0 | 0 | 1003 | 0.15 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1003 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 16 | 81.9 | 0 | 0 | 1003 | 0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-07-24
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.3 | 16.5 | 82.2 | 0 | 0 | 998 | -0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 997 | -0.05 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 2.1 | 16.6 | 81.3 | 0 | 0 | 998 | -0.02 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 998 | 0.16 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 16.5 | 83.3 | 0 | 0 | 998 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 17.7 | 82 | 0 | 0 | 998 | -0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.2 | 3.2 | 11.2 | 76.4 | 0 | 0 | 998 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.4 | 2.5 | 9.8 | 75.3 | 0 | 0 | 998 | -0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 17.5 | 81.4 | 0 | 0 | 998 | 0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.9 | 15.8 | 82.3 | 0 | 0 | 997 | -0.12 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.4 | 15.9 | 82.7 | 0 | 0 | 998 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 997 | -0.06 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 998 | 0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.7 | 16.4 | 82.9 | 0 | 0 | 997 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 996 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.5 | 17.6 | 80.9 | 0 | 0 | 997 | 0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 17.8 | 82 | 0 | 0 | 1004 | -0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.8 | 17.2 | 81 | 0 | 0 | 997 | 0.3 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.1 | 16.8 | 82.1 | 0 | 0 | 998 | -0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18 | 81.7 | 0 | 0 | 998 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 998 | 0.06 | 1 | 9.9 | 0.5 | 4.95
Date | 2020-07-31
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.9 | 16.1 | 82 | 0 | 0 | 1000 | -0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.6 | 16.7 | 82.7 | 0 | 0 | 1000 | -0.03 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.6 | 15.9 | 82.5 | 0 | 0 | 1000 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.7 | 16.3 | 83 | 0 | 0 | 1000 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.4 | 16.9 | 82.7 | 0 | 0 | 1001 | -0.18 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.6 | 16.6 | 82.8 | 0 | 0 | 1000 | -0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.9 | 3.5 | 10.6 | 78 | 0 | 0 | 1001 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 13.1 | 2.9 | 12.6 | 71.4 | 0 | 0 | 1000 | -0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.7 | 17.1 | 81.1 | 0 | 0 | 1000 | 0.11 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 15.9 | 81.9 | 0 | 0 | 1001 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.9 | 15.2 | 82.9 | 0 | 0 | 1000 | 0.07 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 16.3 | 82.9 | 0 | 0 | 1000 | -0.09 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 16.9 | 82.6 | 0 | 0 | 1001 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.4 | 16.1 | 82.5 | 0 | 0 | 1000 | -0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.8 | 17.3 | 81.9 | 0 | 0 | 1000 | -0.21 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.6 | 17 | 81.4 | 0 | 0 | 1000 | -0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 17.8 | 82 | 0 | 0 | 1000 | -0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.3 | 16.6 | 82.1 | 0 | 0 | 1000 | -0.16 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.9 | 16.5 | 82.6 | 0 | 0 | 1000 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.8 | 17.2 | 82 | 0 | 0 | 1000 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.3 | 16.8 | 82.9 | 0 | 0 | 1000 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA10291 | MCERTS certified instrument
Date downloaded | 2020-07-16 13:47 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2020-07-16
Date of last factory calibration | 2020-03-17
Next service due | 2020-09-17
Date of last Gas Check | 2020-03-17
Security code | [DCAD1C07]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | CHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG010MB | 2020-07-16 10:26 | 47.8 | 33.9 | 2.2 | 16.1 | 1004 | -6.05 | 0 | 0 | LOW | fully open | no vacuum change
BHG01MDB | 2020-07-16 10:28 | 47.6 | 34 | 2.1 | 16.3 | 1004 | 170.32 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0035 | 2020-07-16 10:30 | 43 | 34 | 0.8 | 22.2 | 1004 | -4.41 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0036 | 2020-07-16 10:31 | 48.5 | 33.5 | 0.1 | 17.9 | 1004 | -1.23 | 0 | 0 | LOW | closed | vacuum increased
BHGV0036 | 2020-07-16 10:31 | 48.6 | 32.9 | 0.1 | 18.4 | 1004 | -1.51 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0037 | 2020-07-16 10:33 | 68.8 | 32.8 | 0.1 | 0 | 1005 | -0.85 | 0 | 0 | LOW | closed | vacuum increased
BHGV0037 | 2020-07-16 10:33 | 68.7 | 32.9 | 0.1 | 0 | 1005 | -1 | 0 | 0 | LOW | partially open | no vacuum change
BHM010MB | 2020-07-16 10:35 | 55.7 | 41 | 0.1 | 3.2 | 1004 | -5.4 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0018 | 2020-07-16 10:36 | 58 | 42.6 | 0.1 | 0 | 1004 | -4.48 | 3 | 0 | LOW
BHLC004B | 2020-07-16 10:38 | 0.2 | 4.6 | 16.7 | 78.5 | 1004 | 0.36 | 5 | 0 | LOW | closed | no vacuum change
BHR0004B | 2020-07-16 10:39 | 54.8 | 38.1 | 0.3 | 6.8 | 1004 | -4.19 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0015 | 2020-07-16 10:40 | 57.2 | 38.7 | 0.7 | 3.4 | 1004 | -4.37 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0014 | 2020-07-16 10:41 | 54.1 | 40.5 | 0.1 | 5.3 | 1004 | -4.4 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0013 | 2020-07-16 10:42 | 1.2 | 14 | 10.5 | 74.3 | 1005 | 0.11 | 2 | 0 | LOW | closed | no vacuum change
BHGV0016 | 2020-07-16 10:43 | 55.1 | 36.2 | 0.6 | 8.1 | 1005 | -4.25 | 0 | 0 | LOW | fully open | no vacuum change
BHM010MA | 2020-07-16 10:43 | 56 | 38.6 | 0.2 | 5.2 | 1005 | -4.49 | 1 | 0 | LOW | fully open | no vacuum change
BHL000C4 | 2020-07-16 10:45 | 61.9 | 39.3 | 0.1 | 0 | 1004 | -1.32 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0038 | 2020-07-16 10:46 | 37.7 | 28 | 3.8 | 30.5 | 1004 | -3.01 | 0 | 0 | LOW | partially open | vacuum decreased
BHGV0038 | 2020-07-16 10:47 | 38.6 | 26.7 | 4.2 | 30.5 | 1004 | -0.45 | 0 | 0 | LOW | closed | no vacuum change
BHGV0039 | 2020-07-16 10:48 | 67.2 | 32.6 | 0.6 | 0 | 1005 | -4.28 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0039 | 2020-07-16 10:48 | 66.8 | 33.2 | 0.2 | 0 | 1005 | -4.38 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0010 | 2020-07-16 10:51 | 60.6 | 30.8 | 0.1 | 8.5 | 1005 | -0.9 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0010 | 2020-07-16 10:51 | 60.9 | 28.8 | 0.1 | 10.2 | 1005 | -1.49 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0040 | 2020-07-16 10:52 | 56 | 30.5 | 0.6 | 12.9 | 1005 | -3.5 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0040 | 2020-07-16 10:53 | 56.4 | 31.4 | 0.1 | 12.1 | 1005 | -4.21 | 0 | 0 | LOW | partially open | no vacuum change
BHLC001B | 2020-07-16 10:54 | 23.1 | 19.6 | 7.6 | 49.7 | 1005 | -0.16 | 0 | 0 | LOW | closed | no vacuum change
BHGV0009 | 2020-07-16 10:55 | 63.1 | 27.4 | 2.7 | 6.8 | 1005 | -4.43 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0009 | 2020-07-16 10:55 | 61.6 | 29.5 | 0.3 | 8.6 | 1005 | -4.63 | 0 | 0 | LOW | partially open | no vacuum change
BHLC0003 | 2020-07-16 10:57 | 30.4 | 21.9 | 7.6 | 40.1 | 1005 | -4.09 | 0 | 0 | LOW | fully open | vacuum decreased
BHLC0003 | 2020-07-16 10:57 | 30.9 | 21.5 | 7.5 | 40.1 | 1005 | 0.23 | 0 | 0 | LOW | closed | no vacuum change
BHGV0041 | 2020-07-16 11:01 | 57.9 | 35.9 | 0.5 | 5.7 | 1004 | -4.05 | 0 | 0 | LOW | fully open | no vacuum change
BHR00003 | 2020-07-16 11:03 | 26.3 | 18.3 | 9.6 | 45.8 | 1004 | -1.43 | 0 | 0 | LOW | closed | no vacuum change
BHGV0046 | 2020-07-16 11:05 | 54 | 38 | 0.2 | 7.8 | 1004 | -5.42 | 1 | 0 | LOW | partially open | vacuum increased
BHGV0046 | 2020-07-16 11:05 | 53.1 | 38.3 | 0.2 | 8.4 | 1004 | -6.11 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0043 | 2020-07-16 11:12 | 62.8 | 34.9 | 0.2 | 2.1 | 1005 | 0.2 | 0 | 0 | LOW | closed | vacuum increased
BHGV0043 | 2020-07-16 11:13 | 64.1 | 36.5 | 0.1 | 0 | 1005 | -2.28 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0007 | 2020-07-16 11:15 | 72.4 | 28.4 | 0.1 | 0 | 1005 | 0.18 | 0 | 0 | LOW | closed | vacuum increased
BHGV0007 | 2020-07-16 11:15 | 71.7 | 28.4 | 0.1 | 0 | 1005 | -1.11 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0008 | 2020-07-16 11:18 | 26.3 | 15.7 | 9.1 | 48.9 | 1005 | 2.32 | 6 | 0 | LOW | closed | no vacuum change
BHLC002R | 2020-07-16 11:21 | 62 | 33 | 0.2 | 4.8 | 1005 | -4.07 | 0 | 0 | LOW | partially open | vacuum increased
BHLC002R | 2020-07-16 11:21 | 60.6 | 34 | 0.1 | 5.3 | 1005 | -4.19 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0044 | 2020-07-16 11:23 | 66.8 | 31 | 0.5 | 1.7 | 1005 | -0.14 | 0 | 0 | LOW | closed | vacuum increased
BHGV0044 | 2020-07-16 11:24 | 67.2 | 33.4 | 0.1 | 0 | 1005 | -1.51 | 0 | 0 | LOW | partially open | no vacuum change
BHR00001 | 2020-07-16 11:26 | 61 | 33.9 | 0.7 | 4.4 | 1004 | -1.98 | 0 | 0 | LOW | partially open | vacuum increased
BHR00001 | 2020-07-16 11:26 | 61 | 33.9 | 0.8 | 4.3 | 1004 | -4 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0001 | 2020-07-16 11:28 | 60.7 | 34.4 | 0.9 | 4 | 1004 | -3.32 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0004 | 2020-07-16 11:31 | 54.2 | 27.3 | 0.9 | 17.6 | 1005 | -3.8 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0004 | 2020-07-16 11:31 | 55.3 | 27.3 | 0.4 | 17 | 1005 | -3.98 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0003 | 2020-07-16 11:34 | 69.5 | 31.9 | 0.2 | 0 | 1005 | -3.95 | 0 | 0 | LOW | fully open | no vacuum change
BHLC002B | 2020-07-16 11:35 | 49.3 | 32.9 | 3 | 14.8 | 1005 | -2.54 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0021 | 2020-07-16 11:38 | 65 | 35.4 | 0.4 | 0 | 1005 | -2.5 | 1 | 0 | LOW | fully open
BHGV0001 | 2020-07-16 11:39 | 51.6 | 33.5 | 0.2 | 14.7 | 1005 | -4.05 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0045 | 2020-07-16 11:40 | 54.8 | 32.2 | 0.1 | 12.9 | 1005 | -4.08 | 0 | 0 | LOW | fully open | no vacuum change
BHLC002B | 2020-07-16 11:43 | 49.6 | 32.4 | 3 | 15 | 1004 | -0.57 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0022 | 2020-07-16 11:44 | 58.3 | 34.1 | 0.6 | 7 | 1004 | -3.77 | 0 | 0 | LOW | fully open
BHGV0026 | 2020-07-16 11:47 | 59.7 | 37.5 | 0.6 | 2.2 | 1004 | -1.06 | 0 | 0 | LOW | fully open | no vacuum change
BHGV000A | 2020-07-16 11:50 | 59.1 | 40.4 | 0.1 | 0.4 | 1003 | -2.08 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0027 | 2020-07-16 11:52 | 58.5 | 41.2 | 0 | 0.3 | 1004 | -3.56 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0028 | 2020-07-16 11:55 | 57.1 | 39.7 | 0 | 3.2 | 1003 | -3.28 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0029 | 2020-07-16 11:57 | 54.1 | 37.3 | 0.2 | 8.4 | 1003 | -3.54 | 1 | 0 | LOW
BHPRL005 | 2020-07-16 11:59 | 60.2 | 29.6 | 0.7 | 9.5 | 1003 | -0.69 | 0 | 0 | LOW
BHLC0005 | 2020-07-16 12:01 | 60.4 | 29.7 | 0.8 | 9.1 | 1003 | -3.78 | 0 | 0 | LOW | partially open
BHLC006B | 2020-07-16 12:03 | 59.5 | 39.2 | 0.4 | 0.9 | 1003 | -2.69 | 0 | 0 | LOW | fully open | no vacuum change
BHLC0006 | 2020-07-16 12:05 | 2.9 | 6.5 | 15.5 | 75.1 | 1004 | -0.51 | 0 | 0 | LOW | partially open | vacuum decreased
BHLC0006 | 2020-07-16 12:06 | 3.3 | 6 | 14.9 | 75.8 | 1004 | 4.82 | 0 | 0 | LOW | closed | no vacuum change
BHGV0048 | 2020-07-16 12:07 | 55.6 | 32.7 | 0.5 | 11.2 | 1004 | -4.59 | 0 | 0 | LOW | fully open | no vacuum change
BHM050MB | 2020-07-16 12:08 | 55.3 | 35.7 | 0.2 | 8.8 | 1005 | -2.85 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0025 | 2020-07-16 12:10 | 47 | 32.9 | 0.2 | 19.9 | 1005 | -3.44 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0024 | 2020-07-16 12:12 | 60.3 | 37.9 | 0.2 | 1.6 | 1005 | -3.79 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0023 | 2020-07-16 12:14 | 0 | 3.7 | 16.2 | 80.1 | 1005 | 0.81 | 0 | 0 | LOW | closed
BHM050MA | 2020-07-16 12:17 | 55.8 | 36.3 | 0.2 | 7.7 | 1005 | -3.82 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0047 | 2020-07-16 12:18 | 59.3 | 36.7 | 0.6 | 3.4 | 1005 | -1.04 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0047 | 2020-07-16 12:18 | 58.9 | 37.3 | 0.7 | 3.1 | 1005 | -2.89 | 0 | 0 | LOW | partially open | no vacuum change
BHR0006B | 2020-07-16 12:22 | 60 | 37.1 | 0.8 | 2.1 | 1003 | 0.13 | 0 | 0 | LOW | closed | vacuum increased
BHR0006B | 2020-07-16 12:24 | 59.4 | 37.8 | 0.5 | 2.3 | 1003 | -1.26 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0033 | 2020-07-16 12:25 | 49.7 | 37.6 | 0.8 | 11.9 | 1003 | -3.13 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0049 | 2020-07-16 12:26 | 47.1 | 35.8 | 0.3 | 16.8 | 1004 | -4.11 | 0 | 0 | LOW | partially open | no vacuum change
BHG010MA | 2020-07-16 12:30 | 54.9 | 36.2 | 0.3 | 8.6 | 1005 | -5.32 | 0 | 0 | LOW | fully open | no vacuum change
BHG01MDA | 2020-07-16 12:31 | 54.8 | 36.7 | 0.3 | 8.2 | 1005 | 170.3 | 0 | 0 | LOW | fully open | no vacuum change

## August 2020
Date | 2020-08-06
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 1900-01-10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 17.3 | 82.3 | 0 | 0 | 999 | 0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.9 | 15.2 | 81.9 | 0 | 0 | 1000 | -0.25 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1001 | 0.09 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1001 | 0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.8 | 16.1 | 83.1 | 0 | 0 | 1001 | 0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 | [9 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.3 | 2.9 | 14 | 75.8 | 0 | 0 | 1000 | 0.19 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.8 | 8.6 | 13.3 | 63.3 | 0 | 0 | 1000 | 0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.7 | 17.1 | 81.1 | 0 | 0 | 1000 | 0.1 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 15.9 | 81.9 | 0 | 0 | 1000 | -0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.9 | 15.2 | 82.9 | 0 | 0 | 1000 | 0.06 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 16.3 | 82.9 | 0 | 0 | 1000 | -0.08 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 16.9 | 82.6 | 0 | 0 | 1000 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 16.6 | 83.2 | 0 | 0 | 1000 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.7 | 17.4 | 81.9 | 0 | 0 | 1000 | -0.2 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 999 | 0.42 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 17.9 | 81.9 | 0 | 0 | 1000 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.1 | 17.3 | 82.5 | 0 | 0 | 999 | 0 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.9 | 14.8 | 81.3 | 0 | 0 | 1000 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 999 | -0.45 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 16.7 | 82 | 0 | 0 | 999 | 0.59 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-08-13
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 1900-01-09 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 999 | 0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2 | 16.3 | 81.7 | 0 | 0 | 1000 | 0.87 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 1000 | 0.15 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1000 | 0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1 | 16.5 | 82.5 | 0 | 0 | 1000 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 1000 | 0.01 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.2 | 1.3 | 10.5 | 85 | 0 | 0 | 999 | 0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.1 | 8.2 | 13.9 | 63.8 | 0 | 0 | 999 | 0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.7 | 17.1 | 81.1 | 0 | 0 | 999 | 0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 15.8 | 82 | 0 | 0 | 999 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.9 | 15.2 | 82.9 | 0 | 0 | 999 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.5 | 16.3 | 83.2 | 0 | 0 | 999 | 0 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 16.7 | 82.8 | 0 | 0 | 999 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0 | 17 | 82.9 | 0 | 0 | 998 | 0.1 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 998 | 0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 3.5 | 11.7 | 84.8 | 0 | 0 | 998 | -0.2 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 17.8 | 82.2 | 0 | 0 | 998 | -0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 17.5 | 82.5 | 0 | 0 | 998 | 0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.1 | 15.2 | 80.7 | 0 | 0 | 998 | 0.05 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 999 | 0.76 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.4 | 16.7 | 81.9 | 0 | 0 | 999 | 0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-08-19
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 1900-01-09 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.4 | 16.9 | 81.7 | 0 | 0 | 990 | -0.25 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 990 | -0.31 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 990 | 0.1 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 990 | 0.1 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.7 | 16.1 | 83.2 | 0 | 0 | 990 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 990 | 0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 5.4 | 3.1 | 9.9 | 81.6 | 0 | 0 | 990 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.3 | 2.7 | 10.2 | 75.8 | 0 | 0 | 990 | 0.25 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.8 | 17.3 | 80.2 | 0 | 0 | 990 | 0.01 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.9 | 16.8 | 81.3 | 0 | 0 | 990 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.6 | 15.9 | 82.5 | 0 | 0 | 990 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.8 | 81.9 | 0 | 0 | 990 | 0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.8 | 16.1 | 83.1 | 0 | 0 | 990 | -0.17 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.9 | 16.8 | 81.3 | 0 | 0 | 991 | 0.14 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.9 | 17.5 | 81.6 | 0 | 0 | 990 | -0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.3 | 17.4 | 81.3 | 0 | 0 | 990 | 0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 18 | 82 | 0 | 0 | 990 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.9 | 16.9 | 82.2 | 0 | 0 | 990 | 0.19 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.8 | 15.9 | 83.3 | 0 | 0 | 990 | -0.07 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.9 | 17.7 | 81.4 | 0 | 0 | 990 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.5 | 17.9 | 81.6 | 0 | 0 | 990 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-08-27
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 1900-01-09 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 17.5 | 81.3 | 0 | 0 | 999 | -0.22 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 1001 | 0.16 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 1001 | -0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.1 | 2.8 | 10.7 | 82.4 | 0 | 0 | 1001 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 7.3 | 2.6 | 11.9 | 78.2 | 0 | 0 | 1000 | -0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.8 | 17.1 | 81 | 0 | 0 | 1000 | 0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 16.8 | 81.7 | 0 | 0 | 1000 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.4 | 15.3 | 83.3 | 0 | 0 | 1000 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 17 | 81.7 | 0 | 0 | 1000 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 16.2 | 83.2 | 0 | 0 | 1000 | -0.11 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.9 | 16.9 | 81.2 | 0 | 0 | 1000 | 0.07 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 18.2 | 81.5 | 0 | 0 | 1001 | -0.09 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.9 | 17.7 | 81.4 | 0 | 0 | 1000 | -0.21 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 18 | 82 | 0 | 0 | 1000 | -0.01 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.9 | 16.9 | 82.2 | 0 | 0 | 1000 | 0.18 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.4 | 17.7 | 81.9 | 0 | 0 | 1000 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 18.1 | 81.3 | 0 | 0 | 1000 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.7 | 18.6 | 80.7 | 0 | 0 | 1000 | -0.14 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA10291 | MCERTS certified instrument
Date downloaded | 2020-07-16 13:47 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2020-07-16
Date of last factory calibration | 2020-03-17
Next service due | 2020-09-17
Date of last Gas Check | 2020-03-17
Security code | [DCAD1C07]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | CHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG010MB | 2020-08-18 | 47 | 33.9 | 2.2 | 16.9 | 999 | -6.05 | 0 | 0 | LOW | fully open | no vacuum change
BHG01MDB | 2020-08-18 | 47.2 | 34 | 2.1 | 16.7 | 999 | 170.32 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0035 | 2020-08-18 | 43 | 34 | 0.8 | 22.2 | 999 | -4.41 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0036 | 2020-08-18 | 48.5 | 33.5 | 0.1 | 17.9 | 999 | -1.23 | 0 | 0 | LOW | closed | vacuum increased
BHGV0036 | 2020-08-18 | 48.6 | 32.9 | 0.1 | 18.4 | 999 | -1.51 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0037 | 2020-08-18 | 66.9 | 32.8 | 0.1 | 0.2 | 999 | -0.85 | 0 | 0 | LOW | closed | vacuum increased
BHGV0037 | 2020-08-18 | 67.9 | 32.9 | 0.1 | -0.9 | 999 | -1 | 0 | 0 | LOW | partially open | no vacuum change
BHM010MB | 2020-08-18 | 55.7 | 41 | 0.1 | 3.2 | 999 | -5.4 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0018 | 2020-08-18 | 58 | 41.5 | 0.1 | 0.4 | 999 | -4.48 | 3 | 0 | LOW
BHLC004B | 2020-08-18 | 0.3 | 4.6 | 16.7 | 78.4 | 999 | 0.36 | 5 | 0 | LOW | closed | no vacuum change
BHR0004B | 2020-08-18 | 54.8 | 37.9 | 0.3 | 7 | 999 | -4.19 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0015 | 2020-08-18 | 57.2 | 39.9 | 0.7 | 2.2 | 999 | -4.37 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0014 | 2020-08-18 | 53.2 | 40.5 | 0.1 | 6.2 | 999 | -4.4 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0013 | 2020-08-18 | 1.2 | 15 | 10.5 | 73.3 | 999 | 0.11 | 2 | 0 | LOW | closed | no vacuum change
BHGV0016 | 2020-08-18 | 55.2 | 36.2 | 0.6 | 8 | 999 | -4.25 | 0 | 0 | LOW | fully open | no vacuum change
BHM010MA | 2020-08-18 | 56 | 38.6 | 0.2 | 5.2 | 999 | -4.49 | 1 | 0 | LOW | fully open | no vacuum change
BHL000C4 | 2020-08-18 | 60 | 40 | 0.1 | -0.1 | 999 | -1.32 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0038 | 2020-08-18 | 37.7 | 28 | 3.8 | 30.5 | 999 | -3.01 | 0 | 0 | LOW | partially open | vacuum decreased
BHGV0038 | 2020-08-18 | 37.9 | 26.9 | 4.2 | 31 | 999 | -0.45 | 0 | 0 | LOW | closed | no vacuum change
BHGV0039 | 2020-08-18 | 67.2 | 32.6 | 0.6 | -0.4 | 999 | -4.28 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0039 | 2020-08-18 | 64.5 | 31.8 | 0.2 | 3.5 | 999 | -4.38 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0010 | 2020-08-18 | 60.6 | 30.8 | 0.1 | 8.5 | 999 | -0.9 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0010 | 2020-08-18 | 61.2 | 29.9 | 0.1 | 8.8 | 999 | -1.49 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0040 | 2020-08-18 | 56 | 30.5 | 0.6 | 12.9 | 999 | -3.5 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0040 | 2020-08-18 | 56.4 | 31.2 | 0.1 | 12.3 | 999 | -4.21 | 0 | 0 | LOW | partially open | no vacuum change
BHLC001B | 2020-08-18 | 23.1 | 19.6 | 7.6 | 49.7 | 999 | -0.16 | 0 | 0 | LOW | closed | no vacuum change
BHGV0009 | 2020-08-18 | 63.1 | 27.4 | 2.7 | 6.8 | 999 | -4.43 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0009 | 2020-08-18 | 61.6 | 29.5 | 0.3 | 8.6 | 999 | -4.63 | 0 | 0 | LOW | partially open | no vacuum change
BHLC0003 | 2020-08-18 | 30.4 | 21.3 | 7.6 | 40.7 | 999 | -4.09 | 0 | 0 | LOW | fully open | vacuum decreased
BHLC0003 | 2020-08-18 | 30.9 | 21.2 | 7.5 | 40.4 | 999 | 0.23 | 0 | 0 | LOW | closed | no vacuum change
BHGV0041 | 2020-08-18 | 56.9 | 35.9 | 0.5 | 6.7 | 999 | -4.05 | 0 | 0 | LOW | fully open | no vacuum change
BHR00003 | 2020-08-18 | 26.3 | 17.9 | 9.6 | 46.2 | 999 | -1.43 | 0 | 0 | LOW | closed | no vacuum change
BHGV0046 | 2020-08-18 | 54 | 38 | 0.2 | 7.8 | 999 | -5.42 | 1 | 0 | LOW | partially open | vacuum increased
BHGV0046 | 2020-08-18 | 52.6 | 38.3 | 0.3 | 8.8 | 999 | -6.11 | 1 | 0 | LOW | partially open | no vacuum change
BHGV0043 | 2020-08-18 | 62.8 | 34.9 | 0.2 | 2.1 | 999 | 0.2 | 0 | 0 | LOW | closed | vacuum increased
BHGV0043 | 2020-08-18 | 64.1 | 36.5 | 0.1 | -0.7 | 999 | -2.28 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0007 | 2020-08-18 | 70 | 28.4 | 0.1 | 1.5 | 999 | 0.18 | 0 | 0 | LOW | closed | vacuum increased
BHGV0007 | 2020-08-18 | 71.7 | 28.4 | 0.1 | -0.2 | 999 | -1.11 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0008 | 2020-08-18 | 26.3 | 15.7 | 9.1 | 48.9 | 999 | 2.32 | 6 | 0 | LOW | closed | no vacuum change
BHLC002R | 2020-08-18 | 62 | 33 | 0.2 | 4.8 | 999 | -4.07 | 0 | 0 | LOW | partially open | vacuum increased
BHLC002R | 2020-08-18 | 60.6 | 34 | 0.1 | 5.3 | 999 | -4.19 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0044 | 2020-08-18 | 66.8 | 31 | 0.5 | 1.7 | 999 | -0.14 | 0 | 0 | LOW | closed | vacuum increased
BHGV0044 | 2020-08-18 | 67.2 | 33.4 | 0.1 | -0.7 | 999 | -1.51 | 0 | 0 | LOW | partially open | no vacuum change
BHR00001 | 2020-08-18 | 61 | 33.9 | 0.7 | 4.4 | 999 | -1.98 | 0 | 0 | LOW | partially open | vacuum increased
BHR00001 | 2020-08-18 | 61 | 33.9 | 0.8 | 4.3 | 999 | -4 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0001 | 2020-08-18 | 60.7 | 34.4 | 0.9 | 4 | 999 | -3.32 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0004 | 2020-08-18 | 54.2 | 27.3 | 0.9 | 17.6 | 999 | -3.8 | 0 | 0 | LOW | partially open | vacuum increased
BHGV0004 | 2020-08-18 | 55.3 | 27.3 | 0.4 | 17 | 999 | -3.98 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0003 | 2020-08-18 | 69.5 | 31.9 | 0.2 | -1.6 | 999 | -3.95 | 0 | 0 | LOW | fully open | no vacuum change
BHLC002B | 2020-08-18 | 49.3 | 32.9 | 3 | 14.8 | 999 | -2.54 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0021 | 2020-08-18 | 65 | 35.4 | 0.4 | -0.8 | 999 | -2.5 | 1 | 0 | LOW | fully open
BHGV0001 | 2020-08-18 | 51.6 | 33.5 | 0.2 | 14.7 | 999 | -4.05 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0045 | 2020-08-18 | 54.8 | 32.2 | 0.1 | 12.9 | 999 | -4.08 | 0 | 0 | LOW | fully open | no vacuum change
BHLC002B | 2020-08-18 | 49.6 | 32.4 | 3 | 15 | 999 | -0.57 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0022 | 2020-08-18 | 58.3 | 34.1 | 0.6 | 7 | 999 | -3.77 | 0 | 0 | LOW | fully open
BHGV0026 | 2020-08-18 | 59.7 | 37.5 | 0.6 | 2.2 | 999 | -1.06 | 0 | 0 | LOW | fully open | no vacuum change
BHGV000A | 2020-08-18 | 59.1 | 40.4 | 0.1 | 0.4 | 999 | -2.08 | 1 | 0 | LOW | fully open | no vacuum change
BHGV0027 | 2020-08-18 | 58.5 | 41.2 | 0 | 0.3 | 999 | -3.56 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0028 | 2020-08-18 | 57.1 | 39.7 | 0 | 3.2 | 999 | -3.28 | 2 | 0 | LOW | fully open | no vacuum change
BHGV0029 | 2020-08-18 | 54.1 | 37.3 | 0.2 | 8.4 | 999 | -3.54 | 1 | 0 | LOW
BHPRL005 | 2020-08-18 | 60.2 | 29.6 | 0.7 | 9.5 | 999 | -0.69 | 0 | 0 | LOW
BHLC0005 | 2020-08-18 | 60.4 | 29.7 | 0.8 | 9.1 | 999 | -3.78 | 0 | 0 | LOW | partially open
BHLC006B | 2020-08-18 | 59.5 | 39.2 | 0.4 | 0.9 | 999 | -2.69 | 0 | 0 | LOW | fully open | no vacuum change
BHLC0006 | 2020-08-18 | 2.9 | 6.5 | 15.5 | 75.1 | 999 | -0.51 | 0 | 0 | LOW | partially open | vacuum decreased
BHLC0006 | 2020-08-18 | 3.3 | 6 | 14.9 | 75.8 | 999 | 4.82 | 0 | 0 | LOW | closed | no vacuum change
BHGV0048 | 2020-08-18 | 55.6 | 32.7 | 0.5 | 11.2 | 999 | -4.59 | 0 | 0 | LOW | fully open | no vacuum change
BHM050MB | 2020-08-18 | 55.3 | 35.7 | 0.2 | 8.8 | 999 | -2.85 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0025 | 2020-08-18 | 47 | 32.9 | 0.2 | 19.9 | 999 | -3.44 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0024 | 2020-08-18 | 60.3 | 37.9 | 0.2 | 1.6 | 999 | -3.79 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0023 | 2020-08-18 | 0 | 3.7 | 16.2 | 80.1 | 999 | 0.81 | 0 | 0 | LOW | closed
BHM050MA | 2020-08-18 | 55.8 | 36.3 | 0.2 | 7.7 | 999 | -3.82 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0047 | 2020-08-18 | 59.3 | 36.7 | 0.6 | 3.4 | 999 | -1.04 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0047 | 2020-08-18 | 58.9 | 37.3 | 0.7 | 3.1 | 999 | -2.89 | 0 | 0 | LOW | partially open | no vacuum change
BHR0006B | 2020-08-18 | 60 | 37.1 | 0.8 | 2.1 | 999 | 0.13 | 0 | 0 | LOW | closed | vacuum increased
BHR0006B | 2020-08-18 | 59.4 | 37.8 | 0.5 | 2.3 | 999 | -1.26 | 0 | 0 | LOW | partially open | no vacuum change
BHGV0033 | 2020-08-18 | 49.7 | 37.6 | 0.8 | 11.9 | 999 | -3.13 | 0 | 0 | LOW | fully open | no vacuum change
BHGV0049 | 2020-08-18 | 47.1 | 35.8 | 0.3 | 16.8 | 999 | -4.11 | 0 | 0 | LOW | partially open | no vacuum change
BHG010MA | 2020-08-18 | 54.9 | 36.2 | 0.3 | 8.6 | 999 | -5.32 | 0 | 0 | LOW | fully open | no vacuum change
BHG01MDA | 2020-08-18 | 54.8 | 36.7 | 0.3 | 8.2 | 999 | 170.3 | 0 | 0 | LOW | fully open | no vacuum change

## September 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-09-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.8 | 18.8 | 80.4 | 0 | 0 | 1009 | -0.13 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 17.9 | 81.7 | 0 | 0 | 1009 | 0.16 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.4 | 17.1 | 81.5 | 0 | 0 | 1009 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.2 | 3.2 | 11.4 | 83.2 | 0 | 0 | 1009 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.7 | 4.9 | 14.3 | 76.1 | 0 | 0 | 1008 | -0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.6 | 17 | 81.4 | 0 | 0 | 1008 | 0 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 16.5 | 82 | 0 | 0 | 1009 | 0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 15.5 | 83.2 | 0 | 0 | 1008 | -0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.1 | 17.2 | 81.7 | 0 | 0 | 1009 | -0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 16.5 | 82.6 | 0 | 0 | 1009 | -0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.8 | 16.8 | 81.4 | 0 | 0 | 1009 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.4 | 17.3 | 82.3 | 0 | 0 | 1009 | 0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.9 | 17.6 | 81.5 | 0 | 0 | 1009 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0 | 17.9 | 82.1 | 0 | 0 | 1009 | -0.04 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.8 | 16.8 | 82.4 | 0 | 0 | 1009 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.8 | 16.4 | 80.8 | 0 | 0 | 1009 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 18.9 | 80.7 | 0 | 0 | 1008 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 17.6 | 81.1 | 0 | 0 | 1009 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-09-14
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 12 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.9 | 17.9 | 81.2 | 0 | 0 | 1004 | -0.03 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 1004 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 0.8 | 18.4 | 80.8 | 0 | 0 | 1003 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.5 | 18.2 | 81.3 | 0 | 0 | 1003 | -0.11 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 1.3 | 16.7 | 82 | 0 | 0 | 1004 | -0.13 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.8 | 3.2 | 11.1 | 82.9 | 0 | 0 | 1004 | -0.04 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.1 | 3.9 | 14.7 | 77.3 | 0 | 0 | 1003 | 0.09 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17.3 | 81.5 | 0 | 0 | 1003 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.9 | 16.3 | 81.8 | 0 | 0 | 1003 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.3 | 15.8 | 82.9 | 0 | 0 | 1003 | -0.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.2 | 17 | 81.8 | 0 | 0 | 1003 | 0.01 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.3 | 16.9 | 81.8 | 0 | 0 | 1003 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.4 | 16.2 | 82.4 | 0 | 0 | 1003 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 3.8 | 17.6 | 78.6 | 0 | 0 | 1004 | -0.08 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.6 | 17.4 | 82 | 0 | 0 | 1004 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1004 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.8 | 16.8 | 82.4 | 0 | 0 | 1004 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.2 | 16.6 | 80.2 | 0 | 0 | 1004 | -0.07 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.1 | 81.4 | 0 | 0 | 1004 | -0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.7 | 17.6 | 80.7 | 0 | 0 | 1004 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2020-09-23
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.4 | 16.6 | 82 | 0 | 0 | 983 | 0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 17.5 | 82.3 | 0 | 0 | 984 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.4 | 17.2 | 81.4 | 0 | 0 | 984 | -0.16 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | 0 | 0.9 | 17.9 | 81.2 | 0 | 0 | 983 | -0.09 | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 2.3 | 16.4 | 81.3 | 0 | 0 | 983 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.2 | 3.2 | 12.9 | 79.7 | 0 | 0 | 983 | -0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.3 | 3.1 | 15.7 | 78.9 | 0 | 0 | 984 | -0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 17.1 | 81.8 | 0 | 0 | 984 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 16.4 | 82.1 | 0 | 0 | 984 | -0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1 | 15.5 | 83.5 | 0 | 0 | 984 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.9 | 81.8 | 0 | 0 | 984 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 984 | -0.04 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.2 | 16 | 82.8 | 0 | 0 | 984 | -0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 3.7 | 17.4 | 78.9 | 0 | 0 | 984 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 984 | -0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 984 | -0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.7 | 16.6 | 82.7 | 0 | 0 | 983 | -0.01 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 16.3 | 81.2 | 0 | 0 | 983 | 0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 17.3 | 82.1 | 0 | 0 | 983 | -0.15 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 16.9 | 81.8 | 0 | 0 | 983 | -0.04 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12849 | MCERTS certified instrument
Date downloaded | 2020-10-08 12:15 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2020-09-11
Date of last factory calibration | 2020-08-28
Next service due | 2021-02-28
Date of last Gas Check | N/A
Security code | [B5FBD6EC]
ID | DATE | CH4 | CO2 | O2 | BALANCE | CO | H2S | BARO | REL.PRESSURE
|  | % | % | % | % | ppm | ppm | mb | mb
BHG01MDB | 2020-10-08 09:12 | 46.5 | 37.5 | 0.9 | 15.1 | 2 | 0 | 989 | 164.43
BHG010MB | 2020-10-08 09:27 | 46.8 | 37.3 | 0.8 | 15.1 | 1 | 0 | 989 | -23.14
BHGV0035 | 2020-10-08 09:34 | 59.5 | 44.5 | 0 | 0 | 0 | 0 | 989 | -3.32
BHGV0035 | 2020-10-08 09:34 | 59.1 | 44.6 | 0 | 0 | 0 | 0 | 989 | -8.19
BHGV0036 | 2020-10-08 09:36 | 21.1 | 29 | 1.1 | 48.8 | 0 | 0 | 990 | -4.89
BHGV0036 | 2020-10-08 09:36 | 21.3 | 28.7 | 1.1 | 48.9 | 0 | 0 | 990 | 0.04
BHGV0037 | 2020-10-08 09:37 | 27.6 | 28.2 | 2 | 42.2 | 0 | 0 | 990 | -7.39
BHGV0037 | 2020-10-08 09:37 | 27.7 | 27.6 | 1.8 | 42.9 | 0 | 0 | 990 | 0.02
BHM010MB | 2020-10-08 09:39 | 54.7 | 41.6 | 0.3 | 3.4 | 0 | 0 | 990 | -12.19
BHGV0018 | 2020-10-08 09:40 | 58.3 | 44.5 | 0.1 | 0 | 3 | 0 | 990 | -11.86
BHLC004B | 2020-10-08 09:44 | 54.5 | 42.5 | 1.2 | 1.8 | 3 | 0 | 990 | -0.51
BHLC004B | 2020-10-08 09:44 | 54.8 | 42.6 | 1.1 | 1.5 | 3 | 0 | 990 | -11.8
BHR0004B | 2020-10-08 09:45 | 50.7 | 42 | 0.7 | 6.6 | 2 | 0 | 990 | -11.75
BHGV0015 | 2020-10-08 09:46 | 53.6 | 43.1 | 0.2 | 3.1 | 2 | 0 | 990 | -12.06
BHGV0014 | 2020-10-08 09:46 | 52.6 | 42.7 | 0.3 | 4.4 | 2 | 0 | 990 | -11.66
BHGV0013 | 2020-10-08 09:48 | 35.7 | 29.5 | 5.9 | 28.9 | 1 | 0 | 990 | -1.2
BHGV0016 | 2020-10-08 09:49 | 46.2 | 38 | 0.4 | 15.4 | 1 | 0 | 990 | -12.46
BHM010MA | 2020-10-08 09:50 | 54.2 | 42.1 | 0.1 | 3.6 | 2 | 0 | 991 | -12.06
BHGV0038 | 2020-10-08 09:50 | 32.6 | 24.5 | 5.2 | 37.7 | 2 | 0 | 990 | -5.1
BHL000C4 | 2020-10-08 09:52 | 11 | 10.6 | 18.3 | 60.1 | 7 | 0 | 990 | -0.23
BHL000C4 | 2020-10-08 09:52 | 11.2 | 10.1 | 18.2 | 60.5 | 7 | 0 | 990 | -0.2
BHGV0039 | 2020-10-08 09:55 | 66.9 | 36 | 0.2 | 0 | 0 | 0 | 991 | -12.37
BHGV0011 | 2020-10-08 09:57 | 54.9 | 33.6 | 0.4 | 11.1 | 0 | 0 | 991 | -7.58
BHGV0011 | 2020-10-08 09:58 | 55 | 33.6 | 0.2 | 11.2 | 0 | 0 | 991 | -8.25
BHGV0040 | 2020-10-08 10:03 | 42.7 | 34.5 | 0 | 22.8 | 0 | 0 | 991 | -11.84
BHGV0009 | 2020-10-08 10:07 | 38.4 | 32.1 | 0.2 | 29.3 | 0 | 0 | 991 | -11.78
BHGV0009 | 2020-10-08 10:08 | 38.7 | 31.4 | 0 | 29.9 | 1 | 0 | 991 | -5.54
BHLC0003 | 2020-10-08 10:11 | 7.5 | 6.1 | 20 | 66.4 | 0 | 0 | 991 | -6.15
BHGV0301 | 2020-10-08 10:15 | 18.5 | 14.5 | 14.3 | 52.7 | 0 | 0 | 991 | -6.29
BHGV0012 | 2020-10-08 10:18 | 50.9 | 42.5 | 0.3 | 6.3 | 1 | 0 | 991 | -11.97
BHR00003 | 2020-10-08 10:24 | 44.2 | 25 | 7.7 | 23.1 | 0 | 0 | 990 | -0.4
BHGV0046 | 2020-10-08 10:26 | 47.4 | 39.9 | 0.2 | 12.5 | 0 | 0 | 990 | -9.25
BHPRG046 | 2020-10-08 10:26 | 47.5 | 40.3 | 0.4 | 11.8 | 1 | 0 | 990 | -15.06
BHGV0041 | 2020-10-08 10:28 | 53.6 | 40.6 | 0.1 | 5.7 | 0 | 0 | 990 | -12.25
BHPRG041 | 2020-10-08 10:28 | 53.6 | 40.9 | 0 | 5.5 | 1 | 0 | 990 | -12.24
BHGV0043 | 2020-10-08 10:33 | 52.4 | 35.2 | 0 | 12.4 | 0 | 0 | 991 | -7.18
BHGV0043 | 2020-10-08 10:34 | 50.8 | 34.7 | 0 | 14.5 | 0 | 0 | 991 | -8.24
BHGV0007 | 2020-10-08 10:36 | 51.5 | 24.4 | 4.1 | 20 | 0 | 0 | 992 | -5.55
BHGV0007 | 2020-10-08 10:36 | 53.6 | 25.1 | 3.4 | 17.9 | 0 | 0 | 992 | -10.88
BHGV0008 | 2020-10-08 10:38 | 7 | 8.7 | 18.4 | 65.9 | 11 | 0 | 992 | 0.09
BHLC002R | 2020-10-08 10:39 | 46.6 | 33.9 | 0.5 | 19 | 0 | 0 | 992 | -12.33
BHGV0044 | 2020-10-08 10:41 | 58.2 | 33.5 | 0.8 | 7.5 | 0 | 0 | 992 | -5.17
BHGV0044 | 2020-10-08 10:41 | 58.8 | 33.6 | 0.4 | 7.2 | 0 | 0 | 992 | -6.47
BHR00001 | 2020-10-08 10:43 | 57.1 | 36.5 | 0.7 | 5.7 | 0 | 0 | 992 | -13.23
BHR00001 | 2020-10-08 10:44 | 63 | 36.8 | 0.8 | 0 | 0 | 0 | 992 | 5.21
BHR00001 | 2020-10-08 10:46 | 61.8 | 36 | 1.1 | 1.1 | 0 | 0 | 992 | -12.39
BHGV0001 | 2020-10-08 10:46 | 61.6 | 36 | 1.2 | 1.2 | 0 | 0 | 991 | 0.06
BHGV0006 | 2020-10-08 10:54 | 24.5 | 12.9 | 15.3 | 47.3 | 5 | 0 | 992 | -5.81
BHGV0003 | 2020-10-08 10:55 | 61.4 | 35.7 | 0.8 | 2.1 | 0 | 0 | 992 | -12.31
BHGV0004 | 2020-10-08 10:57 | 38 | 34 | 0.4 | 27.6 | 0 | 0 | 992 | -10.97
BHGV0004 | 2020-10-08 10:57 | 37.7 | 34.1 | 0.2 | 28 | 0 | 0 | 992 | 0
BHLC002B | 2020-10-08 10:59 | 31.6 | 25.2 | 8.7 | 34.5 | 0 | 0 | 992 | -12.32
BHLC002B | 2020-10-08 10:59 | 31.6 | 24.8 | 8.4 | 35.2 | 0 | 0 | 992 | 0.05
BHGV0045 | 2020-10-08 11:01 | 36.7 | 32.7 | 0.7 | 29.9 | 0 | 0 | 992 | -12.7
BHGV0045 | 2020-10-08 11:02 | 36.5 | 33.3 | 0.1 | 30.1 | 0 | 0 | 992 | 0
BHLC002B | 2020-10-08 11:04 | 17.7 | 13.7 | 17.1 | 51.5 | 0 | 0 | 991 | -4.37
BHLC002B | 2020-10-08 11:04 | 17.7 | 13.7 | 16.8 | 51.8 | 0 | 0 | 991 | 0.07
BHGV0026 | 2020-10-08 11:08 | 46.4 | 36.1 | 0.5 | 17 | 0 | 0 | 991 | -12.59
BHGV000A | 2020-10-08 11:13 | 59.1 | 45.3 | 0 | 0 | 2 | 0 | 991 | -10.79
BHGV0027 | 2020-10-08 11:14 | 51 | 45.2 | 0.6 | 3.2 | 0 | 0 | 991 | -12.88
BHGV0047 | 2020-10-08 11:17 | 61.2 | 40.6 | 0.1 | 0 | 0 | 0 | 991 | 1.34
BHGV0047 | 2020-10-08 11:18 | 61.3 | 40.7 | 0 | 0 | 0 | 1 | 991 | -7.06
BHGV0024 | 2020-10-08 11:21 | 60.9 | 40.9 | 0.4 | 0 | 0 | 0 | 992 | -12.89
BHM050MB | 2020-10-08 11:24 | 51.8 | 41.4 | 0.3 | 6.5 | 0 | 0 | 992 | -15.44
BHGV0025 | 2020-10-08 11:27 | 37 | 33.2 | 0.7 | 29.1 | 0 | 0 | 992 | -6.8
BHGV0025 | 2020-10-08 11:28 | 37.2 | 33.5 | 0.8 | 28.5 | 0 | 0 | 724 | 0
BHGV0023 | 2020-10-08 11:30 | 37.3 | 33.6 | 1.3 | 27.8 | 0 | 0 | 992 | 0.02
BHGV0048 | 2020-10-08 11:31 | 51.7 | 40.3 | 0 | 8 | 0 | 0 | 992 | -13.31
BHGV0023 | 2020-10-08 11:32 | 62.3 | 40.9 | 0.2 | 0 | 0 | 0 | 992 | -13.08
BHGV0022 | 2020-10-08 11:34 | 69 | 35.8 | 0 | 0 | 0 | 0 | 992 | 0.17
BHLC0006 | 2020-10-08 11:38 | 59.9 | 38.3 | 0.6 | 1.2 | 1 | 0 | 992 | -0.03
BHLC0006 | 2020-10-08 11:39 | 58.2 | 38.2 | 0.6 | 3 | 1 | 0 | 992 | -1.06
BHLC006B | 2020-10-08 11:40 | 56.2 | 39.7 | 0.5 | 3.6 | 0 | 0 | 992 | -12.57
BHLC0005 | 2020-10-08 11:42 | 57.4 | 44.3 | 0.4 | 0 | 2 | 1 | 991 | 0.05
BHLC0005 | 2020-10-08 11:43 | 57.7 | 44.4 | 0.3 | 0 | 2 | 0 | 991 | -1.45
BHGV0029 | 2020-10-08 11:44 | 57.5 | 42.3 | 0.1 | 0.1 | 1 | 0 | 991 | -13.67
BHGV0028 | 2020-10-08 11:46 | 55.9 | 42.2 | 0 | 1.9 | 1 | 0 | 991 | -12.59
BHGV000B | 2020-10-08 11:49 | 45.4 | 40.1 | 0.1 | 14.4 | 0 | 0 | 991 | -12.9
BHGV0030 | 2020-10-08 11:50 | 54.9 | 39.9 | 0.1 | 5.1 | 1 | 0 | 991 | -11.76
BHGV000C | 2020-10-08 11:51 | 58.6 | 43.6 | 0.1 | 0 | 1 | 0 | 991 | -11.46
BHR00005 | 2020-10-08 11:53 | 39.1 | 33.6 | 6.6 | 20.7 | 2 | 0 | 991 | -10.28
BHR00005 | 2020-10-08 11:53 | 39.4 | 32.9 | 6.9 | 20.8 | 2 | 0 | 991 | -0.09
BHGV0031 | 2020-10-08 11:54 | 53.8 | 41.3 | 0.4 | 4.5 | 0 | 0 | 991 | -12.25
BHGV0032 | 2020-10-08 11:58 | 48 | 39 | 3.7 | 9.3 | 1 | 0 | 991 | -5.79
BHGV0033 | 2020-10-08 12:00 | 32.3 | 31.8 | 2.5 | 33.4 | 0 | 0 | 992 | -11.98
BHGV0033 | 2020-10-08 12:00 | 32.7 | 31.9 | 2.3 | 33.1 | 0 | 0 | 992 | -0.09
BHR0006B | 2020-10-08 12:02 | 0.1 | 6.4 | 22 | 71.5 | 0 | 0 | 992 | 2.17
BHGV0049 | 2020-10-08 12:03 | 33.2 | 36.8 | 1.4 | 28.6 | 0 | 0 | 992 | -7.56
BHGW0034 | 2020-10-08 12:05 | 30.7 | 23.3 | 1.5 | 44.5 | 0 | 0 | 993 | -7.12
BHGW0034 | 2020-10-08 12:06 | 30.3 | 23.6 | 0.6 | 45.5 | 0 | 0 | 993 | -0.08
BHG010MA | 2020-10-08 12:09 | 49.8 | 38 | 0.9 | 11.3 | 0 | 0 | 993 | -25.67
BHG01MDA | 2020-10-08 12:10 | 50.6 | 38.9 | 0.5 | 10 | 0 | 0 | 993 | 162.38

## October 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-10-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 21 | 78.8 | 0 | 0 | 994 | 0.12 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.7 | 22 | 75.2 | 0 | 0 | 995 | 1.65 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 15 | 3.4 | 15.8 | 65.8 | 0 | 0 | 995 | 0.23 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.2 | 7.3 | 20 | 60.5 | 0 | 0 | 995 | -0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17 | 81.8 | 0 | 0 | 995 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 16.5 | 82.1 | 0 | 0 | 995 | -0.01 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.8 | 22.8 | 75.3 | 0 | 0 | 995 | -0.1 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.2 | 16.8 | 82 | 0 | 0 | 995 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 20.4 | 79.6 | 0 | 0 | 995 | -1.76 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.1 | 20.7 | 79.1 | 0 | 0 | 995 | 0.13 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.1 | 20.5 | 79.4 | 0 | 0 | 994 | 0.71 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.9 | 12.2 | 85.8 | 0 | 0 | 993 | -0.28 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 17.5 | 82.2 | 0 | 0 | 994 | -0.03 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Buried | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.6 | 16.5 | 82.9 | 0 | 0 | 995 | -0.04 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.8 | 17.7 | 76.5 | 0 | 0 | 994 | 0.58 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 20.9 | 79 | 0 | 0 | 994 | -0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.2 | 16.8 | 82 | 0 | 0 | 994 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-10-16
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 13 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.5 | 17.4 | 81.1 | 0 | 0 | 1010 | 0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.3 | 17.8 | 80.9 | 0 | 0 | 1011 | -0.06 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.1 | 3.2 | 12.5 | 80.2 | 0 | 0 | 1011 | -0.18 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 7.9 | 6.6 | 14.7 | 70.8 | 0 | 0 | 1010 | -0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 17 | 81.9 | 0 | 0 | 1010 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.6 | 16.8 | 81.6 | 0 | 0 | 1010 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.9 | 20 | 78 | 0 | 0 | 1010 | -0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.3 | 16.5 | 82.2 | 0 | 0 | 1010 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 19.7 | 80.1 | 0 | 0 | 1011 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 19.3 | 80.5 | 0 | 0 | 1011 | 0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.2 | 19.1 | 80.7 | 0 | 0 | 1011 | -0.16 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.2 | 13.9 | 83.9 | 0 | 0 | 1011 | -0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.4 | 17.3 | 82.3 | 0 | 0 | 1011 | -0.05 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.8 | 16.9 | 81.3 | 0 | 0 | 1011 | -0.19 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 18.4 | 81.1 | 0 | 0 | 1011 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.9 | 17.8 | 81.3 | 0 | 0 | 1011 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-10-21
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.4 | 17.1 | 81.5 | 0 | 0 | 977 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.5 | 18.2 | 80.3 | 0 | 0 | 977 | -0.07 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 6.4 | 3.2 | 11.4 | 78.6 | 0 | 0 | 977 | 0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 8.6 | 6.9 | 12.9 | 71.6 | 0 | 0 | 977 | 0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 17.6 | 81.1 | 0 | 0 | 977 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 17.2 | 81.3 | 0 | 0 | 977 | 0 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.2 | 19.9 | 77.8 | 0 | 0 | 977 | -0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.4 | 16 | 82.6 | 0 | 0 | 977 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 18.9 | 81 | 0 | 0 | 977 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 18.2 | 81.5 | 0 | 0 | 977 | -0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.3 | 18.7 | 81 | 0 | 0 | 977 | -0.18 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.5 | 14.6 | 83.9 | 0 | 0 | 977 | -0.01 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 977 | -0.04 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.2 | 16.6 | 81.2 | 0 | 0 | 977 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.7 | 17.8 | 81.5 | 0 | 0 | 978 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.5 | 17.6 | 80.9 | 0 | 0 | 977 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-10-28
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 18 | 81.8 | 0 | 0 | 979 | -0.11 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.8 | 16.7 | 81.4 | 0 | 0 | 980 | 0.13 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | 0 | 1.4 | 18.3 | 80.3 | 0 | 0 | 980 | -0.01 | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 10 | 2.4 | 18.8 | 68.8 | 0 | 0 | 979 | -0.17 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.4 | 9.2 | 13.8 | 61.6 | 0 | 0 | 979 | -0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17.5 | 81.3 | 0 | 0 | 979 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 17.1 | 81.5 | 0 | 0 | 979 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.6 | 16.6 | 80.7 | 0 | 0 | 980 | 0.03 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.7 | 82.2 | 0 | 0 | 979 | -0.82 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.9 | 17.4 | 81.6 | 0 | 0 | 979 | -0.12 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.1 | 17.5 | 82.3 | 0 | 0 | 979 | -0.19 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 2.6 | 9.1 | 88.2 | 0 | 0 | 979 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.2 | 17.1 | 82.7 | 0 | 0 | 980 | -0.02 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 6.1 | 12.6 | 81.2 | 0 | 0 | 978 | -0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.2 | 15.1 | 84.6 | 0 | 0 | 979 | 0.73 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12849 | MCERTS certified instrument
Date downloaded | 2020-10-08 12:15 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2020-09-11
Date of last factory calibration | 2020-08-28
Next service due | 2021-02-28
Date of last Gas Check | N/A
Security code | [B5FBD6EC]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | CHOSEN 1 | CHOSEN 2 | CHOSEN 3
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2020-10-08 09:12 | 46.5 | 37.5 | 0.9 | 15.1 | 989 | 164.43 | 2 | 0 | fully open | no vacuum change
BHG010MB | 2020-10-08 09:27 | 46.8 | 37.3 | 0.8 | 15.1 | 989 | -23.14 | 1 | 0 | fully open | no vacuum change
BHGV0035 | 2020-10-08 09:34 | 59.5 | 44.5 | 0 | 0 | 989 | -3.32 | 0 | 0 | closed | vacuum increased
BHGV0035 | 2020-10-08 09:34 | 59.1 | 44.6 | 0 | 0 | 989 | -8.19 | 0 | 0 | partially open | no vacuum change
BHGV0036 | 2020-10-08 09:36 | 21.1 | 29 | 1.1 | 48.8 | 990 | -4.89 | 0 | 0 | partially open | vacuum decreased
BHGV0036 | 2020-10-08 09:36 | 21.3 | 28.7 | 1.1 | 48.9 | 990 | 0.04 | 0 | 0 | closed | no vacuum change
BHGV0037 | 2020-10-08 09:37 | 27.6 | 28.2 | 2 | 42.2 | 990 | -7.39 | 0 | 0 | partially open | vacuum decreased
BHGV0037 | 2020-10-08 09:37 | 27.7 | 27.6 | 1.8 | 42.9 | 990 | 0.02 | 0 | 0 | closed | no vacuum change
BHM010MB | 2020-10-08 09:39 | 54.7 | 41.6 | 0.3 | 3.4 | 990 | -12.19 | 0 | 0 | fully open | no vacuum change
BHGV0018 | 2020-10-08 09:40 | 58.3 | 44.5 | 0.1 | 0 | 990 | -11.86 | 3 | 0 | fully open | no vacuum change
BHLC004B | 2020-10-08 09:44 | 54.5 | 42.5 | 1.2 | 1.8 | 990 | -0.51 | 3 | 0 | closed | vacuum increased
BHLC004B | 2020-10-08 09:44 | 54.8 | 42.6 | 1.1 | 1.5 | 990 | -11.8 | 3 | 0 | partially open | no vacuum change
BHR0004B | 2020-10-08 09:45 | 50.7 | 42 | 0.7 | 6.6 | 990 | -11.75 | 2 | 0 | partially open | no vacuum change
BHGV0015 | 2020-10-08 09:46 | 53.6 | 43.1 | 0.2 | 3.1 | 990 | -12.06 | 2 | 0 | fully open | no vacuum change
BHGV0014 | 2020-10-08 09:46 | 52.6 | 42.7 | 0.3 | 4.4 | 990 | -11.66 | 2 | 0 | fully open | no vacuum change
BHGV0013 | 2020-10-08 09:48 | 35.7 | 29.5 | 5.9 | 28.9 | 990 | -1.2 | 1 | 0 | closed | no vacuum change
BHGV0016 | 2020-10-08 09:49 | 46.2 | 38 | 0.4 | 15.4 | 990 | -12.46 | 1 | 0 | fully open | no vacuum change
BHM010MA | 2020-10-08 09:50 | 54.2 | 42.1 | 0.1 | 3.6 | 991 | -12.06 | 2 | 0 | fully open | no vacuum change
BHGV0038 | 2020-10-08 09:50 | 32.6 | 24.5 | 5.2 | 37.7 | 990 | -5.1 | 2 | 0 | closed | no vacuum change
BHL000C4 | 2020-10-08 09:52 | 11 | 10.6 | 18.3 | 60.1 | 990 | -0.23 | 7 | 0 | partially open | vacuum decreased
BHL000C4 | 2020-10-08 09:52 | 11.2 | 10.1 | 18.2 | 60.5 | 990 | -0.2 | 7 | 0 | closed | no vacuum change
BHGV0039 | 2020-10-08 09:55 | 66.9 | 36 | 0.2 | 0 | 991 | -12.37 | 0 | 0 | partially open | vacuum increased
BHGV0011 | 2020-10-08 09:57 | 54.9 | 33.6 | 0.4 | 11.1 | 991 | -7.58 | 0 | 0 | partially open | vacuum increased
BHGV0011 | 2020-10-08 09:58 | 55 | 33.6 | 0.2 | 11.2 | 991 | -8.25 | 0 | 0 | partially open | no vacuum change
BHGV0040 | 2020-10-08 10:03 | 42.7 | 34.5 | 0 | 22.8 | 991 | -11.84 | 0 | 0 | partially open | no vacuum change
BHGV0009 | 2020-10-08 10:07 | 38.4 | 32.1 | 0.2 | 29.3 | 991 | -11.78 | 0 | 0 | partially open | vacuum decreased
BHGV0009 | 2020-10-08 10:08 | 38.7 | 31.4 | 0 | 29.9 | 991 | -5.54 | 1 | 0 | closed | no vacuum change
BHLC0003 | 2020-10-08 10:11 | 7.5 | 6.1 | 20 | 66.4 | 991 | -6.15 | 0 | 0 | closed | no vacuum change
BHGV0301 | 2020-10-08 10:15 | 18.5 | 14.5 | 14.3 | 52.7 | 991 | -6.29 | 0 | 0 | fully open | vacuum decreased
BHGV0012 | 2020-10-08 10:18 | 50.9 | 42.5 | 0.3 | 6.3 | 991 | -11.97 | 1 | 0 | fully open | no vacuum change
BHR00003 | 2020-10-08 10:24 | 44.2 | 25 | 7.7 | 23.1 | 990 | -0.4 | 0 | 0 | closed | no vacuum change
BHGV0046 | 2020-10-08 10:26 | 47.4 | 39.9 | 0.2 | 12.5 | 990 | -9.25 | 0 | 0 | partially open
BHPRG046 | 2020-10-08 10:26 | 47.5 | 40.3 | 0.4 | 11.8 | 990 | -15.06 | 1 | 0
BHGV0041 | 2020-10-08 10:28 | 53.6 | 40.6 | 0.1 | 5.7 | 990 | -12.25 | 0 | 0 | fully open
BHPRG041 | 2020-10-08 10:28 | 53.6 | 40.9 | 0 | 5.5 | 990 | -12.24 | 1 | 0
BHGV0043 | 2020-10-08 10:33 | 52.4 | 35.2 | 0 | 12.4 | 991 | -7.18 | 0 | 0 | closed | vacuum increased
BHGV0043 | 2020-10-08 10:34 | 50.8 | 34.7 | 0 | 14.5 | 991 | -8.24 | 0 | 0 | partially open | no vacuum change
BHGV0007 | 2020-10-08 10:36 | 51.5 | 24.4 | 4.1 | 20 | 992 | -5.55 | 0 | 0 | closed | vacuum increased
BHGV0007 | 2020-10-08 10:36 | 53.6 | 25.1 | 3.4 | 17.9 | 992 | -10.88 | 0 | 0 | partially open | no vacuum change
BHGV0008 | 2020-10-08 10:38 | 7 | 8.7 | 18.4 | 65.9 | 992 | 0.09 | 11 | 0 | closed | no vacuum change
BHLC002R | 2020-10-08 10:39 | 46.6 | 33.9 | 0.5 | 19 | 992 | -12.33 | 0 | 0 | partially open | no vacuum change
BHGV0044 | 2020-10-08 10:41 | 58.2 | 33.5 | 0.8 | 7.5 | 992 | -5.17 | 0 | 0 | closed | vacuum increased
BHGV0044 | 2020-10-08 10:41 | 58.8 | 33.6 | 0.4 | 7.2 | 992 | -6.47 | 0 | 0 | partially open
BHR00001 | 2020-10-08 10:43 | 57.1 | 36.5 | 0.7 | 5.7 | 992 | -13.23 | 0 | 0 | fully open | no vacuum change
BHR00001 | 2020-10-08 10:44 | 63 | 36.8 | 0.8 | 0 | 992 | 5.21 | 0 | 0 | closed | vacuum increased
BHR00001 | 2020-10-08 10:46 | 61.8 | 36 | 1.1 | 1.1 | 992 | -12.39 | 0 | 0 | partially open | no vacuum change
BHGV0001 | 2020-10-08 10:46 | 61.6 | 36 | 1.2 | 1.2 | 991 | 0.06 | 0 | 0 | partially open | no vacuum change
BHGV0006 | 2020-10-08 10:54 | 24.5 | 12.9 | 15.3 | 47.3 | 992 | -5.81 | 5 | 0 | closed | no vacuum change
BHGV0003 | 2020-10-08 10:55 | 61.4 | 35.7 | 0.8 | 2.1 | 992 | -12.31 | 0 | 0 | fully open | no vacuum change
BHGV0004 | 2020-10-08 10:57 | 38 | 34 | 0.4 | 27.6 | 992 | -10.97 | 0 | 0 | partially open | vacuum decreased
BHGV0004 | 2020-10-08 10:57 | 37.7 | 34.1 | 0.2 | 28 | 992 | 0 | 0 | 0 | closed | no vacuum change
BHLC002B | 2020-10-08 10:59 | 31.6 | 25.2 | 8.7 | 34.5 | 992 | -12.32 | 0 | 0 | partially open | vacuum decreased
BHLC002B | 2020-10-08 10:59 | 31.6 | 24.8 | 8.4 | 35.2 | 992 | 0.05 | 0 | 0 | closed | no vacuum change
BHGV0045 | 2020-10-08 11:01 | 36.7 | 32.7 | 0.7 | 29.9 | 992 | -12.7 | 0 | 0 | fully open | vacuum decreased
BHGV0045 | 2020-10-08 11:02 | 36.5 | 33.3 | 0.1 | 30.1 | 992 | 0 | 0 | 0 | closed | no vacuum change
BHLC002B | 2020-10-08 11:04 | 17.7 | 13.7 | 17.1 | 51.5 | 991 | -4.37 | 0 | 0 | partially open | vacuum decreased
BHLC002B | 2020-10-08 11:04 | 17.7 | 13.7 | 16.8 | 51.8 | 991 | 0.07 | 0 | 0 | closed | no vacuum change
BHGV0026 | 2020-10-08 11:08 | 46.4 | 36.1 | 0.5 | 17 | 991 | -12.59 | 0 | 0 | fully open | no vacuum change
BHGV000A | 2020-10-08 11:13 | 59.1 | 45.3 | 0 | 0 | 991 | -10.79 | 2 | 0 | fully open | no vacuum change
BHGV0027 | 2020-10-08 11:14 | 51 | 45.2 | 0.6 | 3.2 | 991 | -12.88 | 0 | 0 | fully open | no vacuum change
BHGV0047 | 2020-10-08 11:17 | 61.2 | 40.6 | 0.1 | 0 | 991 | 1.34 | 0 | 0 | closed | vacuum increased
BHGV0047 | 2020-10-08 11:18 | 61.3 | 40.7 | 0 | 0 | 991 | -7.06 | 0 | 1 | partially open | no vacuum change
BHGV0024 | 2020-10-08 11:21 | 60.9 | 40.9 | 0.4 | 0 | 992 | -12.89 | 0 | 0 | fully open | no vacuum change
BHM050MB | 2020-10-08 11:24 | 51.8 | 41.4 | 0.3 | 6.5 | 992 | -15.44 | 0 | 0 | fully open | no vacuum change
BHGV0025 | 2020-10-08 11:27 | 37 | 33.2 | 0.7 | 29.1 | 992 | -6.8 | 0 | 0 | partially open | vacuum decreased
BHGV0025 | 2020-10-08 11:28 | 37.2 | 33.5 | 0.8 | 28.5 | 724 | 0 | 0 | 0 | closed | no vacuum change
BHGV0023 | 2020-10-08 11:30 | 37.3 | 33.6 | 1.3 | 27.8 | 992 | 0.02 | 0 | 0 | closed | no vacuum change
BHGV0048 | 2020-10-08 11:31 | 51.7 | 40.3 | 0 | 8 | 992 | -13.31 | 0 | 0 | fully open | no vacuum change
BHGV0023 | 2020-10-08 11:32 | 62.3 | 40.9 | 0.2 | 0 | 992 | -13.08 | 0 | 0 | no vacuum change
BHGV0022 | 2020-10-08 11:34 | 69 | 35.8 | 0 | 0 | 992 | 0.17 | 0 | 0 | fully open
BHLC0006 | 2020-10-08 11:38 | 59.9 | 38.3 | 0.6 | 1.2 | 992 | -0.03 | 1 | 0 | closed |  | vacuum increased
BHLC0006 | 2020-10-08 11:39 | 58.2 | 38.2 | 0.6 | 3 | 992 | -1.06 | 1 | 0 | partially open | no vacuum change
BHLC006B | 2020-10-08 11:40 | 56.2 | 39.7 | 0.5 | 3.6 | 992 | -12.57 | 0 | 0 | fully open | no vacuum change
BHLC0005 | 2020-10-08 11:42 | 57.4 | 44.3 | 0.4 | 0 | 991 | 0.05 | 2 | 1 | closed | vacuum increased
BHLC0005 | 2020-10-08 11:43 | 57.7 | 44.4 | 0.3 | 0 | 991 | -1.45 | 2 | 0 | partially open | no vacuum change
BHGV0029 | 2020-10-08 11:44 | 57.5 | 42.3 | 0.1 | 0.1 | 991 | -13.67 | 1 | 0 | fully open | no vacuum change
BHGV0028 | 2020-10-08 11:46 | 55.9 | 42.2 | 0 | 1.9 | 991 | -12.59 | 1 | 0 | fully open | no vacuum change
BHGV000B | 2020-10-08 11:49 | 45.4 | 40.1 | 0.1 | 14.4 | 991 | -12.9 | 0 | 0 | fully open | no vacuum change
BHGV0030 | 2020-10-08 11:50 | 54.9 | 39.9 | 0.1 | 5.1 | 991 | -11.76 | 1 | 0 | fully open | no vacuum change
BHGV000C | 2020-10-08 11:51 | 58.6 | 43.6 | 0.1 | 0 | 991 | -11.46 | 1 | 0 | fully open | no vacuum change
BHR00005 | 2020-10-08 11:53 | 39.1 | 33.6 | 6.6 | 20.7 | 991 | -10.28 | 2 | 0 | partially open | no vacuum change
BHR00005 | 2020-10-08 11:53 | 39.4 | 32.9 | 6.9 | 20.8 | 991 | -0.09 | 2 | 0 | closed | no vacuum change
BHGV0031 | 2020-10-08 11:54 | 53.8 | 41.3 | 0.4 | 4.5 | 991 | -12.25 | 0 | 0 | fully open | no vacuum change
BHGV0032 | 2020-10-08 11:58 | 48 | 39 | 3.7 | 9.3 | 991 | -5.79 | 1 | 0 | fully open | no vacuum change
BHGV0033 | 2020-10-08 12:00 | 32.3 | 31.8 | 2.5 | 33.4 | 992 | -11.98 | 0 | 0 | partially open | vacuum decreased
BHGV0033 | 2020-10-08 12:00 | 32.7 | 31.9 | 2.3 | 33.1 | 992 | -0.09 | 0 | 0 | closed | no vacuum change
BHR0006B | 2020-10-08 12:02 | 0.1 | 6.4 | 22 | 71.5 | 992 | 2.17 | 0 | 0 | closed | no vacuum change
BHGV0049 | 2020-10-08 12:03 | 33.2 | 36.8 | 1.4 | 28.6 | 992 | -7.56 | 0 | 0 | closed | no vacuum change
BHGW0034 | 2020-10-08 12:05 | 30.7 | 23.3 | 1.5 | 44.5 | 993 | -7.12 | 0 | 0 | partially open | vacuum decreased
BHGW0034 | 2020-10-08 12:06 | 30.3 | 23.6 | 0.6 | 45.5 | 993 | -0.08 | 0 | 0 | closed | no vacuum change
BHG010MA | 2020-10-08 12:09 | 49.8 | 38 | 0.9 | 11.3 | 993 | -25.67 | 0 | 0 | fully open | no vacuum change
BHG01MDA | 2020-10-08 12:10 | 50.6 | 38.9 | 0.5 | 10 | 993 | 162.38 | 0 | 0 | fully open | no vacuum change

## November 2020
Date | 2020-11-04
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.9 | 17.3 | 80.8 | 0 | 0 | 1019 | -0.11 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 8.8 | 3.5 | 11.7 | 75.6 | 0 | 0 | 1019 | 0.02 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 13.9 | 7.6 | 12.2 | 66.3 | 0 | 0 | 1019 | -0.05 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 17 | 81.9 | 0 | 0 | 1019 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 17.3 | 81.2 | 0 | 0 | 1019 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | Flooded | [7 empty] | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.2 | 18.3 | 81.5 | 0 | 0 | 1019 | 0 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 18.6 | 81 | 0 | 0 | 1019 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.5 | 17.9 | 81.6 | 0 | 0 | 1019 | 0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.9 | 14.1 | 84 | 0 | 0 | 1019 | 0.03 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.3 | 17 | 82.7 | 0 | 0 | 1019 | -0.02 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.7 | 17.5 | 79.8 | 0 | 0 | 1019 | -0.07 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.1 | 17.9 | 81 | 0 | 0 | 1019 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.9 | 17.3 | 81.8 | 0 | 0 | 1019 | -0.07 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-11-11
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 1.1 | 20.3 | 78.5 | 0 | 0 | 995 | -0.29 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.2 | 1.6 | 20 | 78.2 | 0 | 0 | 994 | -0.17 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.3 | 3.2 | 12.4 | 72.8 | 0 | 0 | 994 | -0.15 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.2 | 7.5 | 15.4 | 73.9 | 0 | 0 | 994 | -0.31 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17.2 | 81.6 | 0 | 0 | 994 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 17.4 | 61.3 | 0 | 0 | 994 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.3 | 16.9 | 80.7 | 0 | 0 | 993 | -2.08 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0.2 | 1.1 | 20 | 78.7 | 0 | 0 | 995 | -0.17 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.7 | 20 | 79.2 | 0 | 0 | 994 | 2.78 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.2 | 1.5 | 19.7 | 78.6 | 0 | 0 | 993 | -0.12 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 2 | 19.7 | 78.1 | 0 | 0 | 995 | -0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.3 | 15.5 | 83.1 | 0 | 0 | 993 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.2 | 17.2 | 82.6 | 0 | 0 | 993 | -0.03 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 2.1 | 18.4 | 79.4 | 0 | 0 | 994 | -0.99 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.7 | 20.4 | 78.8 | 0 | 0 | 994 | 0.75 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 1.3 | 19.7 | 78.9 | 0 | 0 | 994 | -0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-11-17
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 19.8 | 79 | 0 | 0 | 1007 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 1.4 | 19.6 | 78.9 | 0 | 0 | 1007 | -0.02 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.9 | 3.5 | 12.8 | 71.6 | 0 | 0 | 1008 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.1 | 6.7 | 14.7 | 74.5 | 0 | 0 | 1008 | -0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.1 | 17.2 | 81.7 | 0 | 0 | 1008 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 17.3 | 81.3 | 0 | 0 | 1008 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 1.8 | 16.5 | 81.6 | 0 | 0 | 1008 | -0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.7 | 19.4 | 79.9 | 0 | 0 | 1008 | -0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.3 | 19.6 | 80.1 | 0 | 0 | 1007 | -0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.7 | 19.4 | 78.9 | 0 | 0 | 1008 | 0.03 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 1008 | -0.11 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.1 | 15.8 | 83.1 | 0 | 0 | 1008 | -0.08 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 1008 | -0.04 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.5 | 18.1 | 80.4 | 0 | 0 | 1008 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 19.7 | 79.9 | 0 | 0 | 1008 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 19.3 | 79.1 | 0 | 0 | 1008 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-11-25
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 992 | 0.21 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 993 | 0.74 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.2 | 18.1 | 81.7 | 0 | 0 | 994 | 0.13 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.6 | 3.4 | 12.1 | 74.9 | 0 | 0 | 994 | 0.12 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.1 | 8.7 | 13.8 | 62.4 | 0 | 0 | 993 | 0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.2 | 17.1 | 81.7 | 0 | 0 | 994 | -0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 17 | 81.7 | 0 | 0 | 993 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.5 | 13.7 | 82.8 | 0 | 0 | 994 | 0.41 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 993 | -0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 18.1 | 81.6 | 0 | 0 | 993 | -0.76 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0 | 16.7 | 83.3 | 0 | 0 | 992 | 0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 3 | 16.8 | 80.1 | 0 | 0 | 992 | 0.16 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.3 | 17.1 | 82.6 | 0 | 0 | 992 | -0.03 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.8 | 14.6 | 79.6 | 0 | 0 | 992 | 0.36 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.4 | 82.5 | 0 | 0 | 992 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.3 | 17.3 | 81.4 | 0 | 0 | 992 | 0.09 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA10292 | MCERTS certified instrument
Date downloaded | 2020-11-05 16:06 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | 2020-10-22
Date of last factory calibration | 2020-05-06
Next service due | 2020-11-06
Date of last Gas Check | 2020-05-06
Security code | [58A4659C]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | ANSWER 1 | ANSWER 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG01MDB | 2020-11-05 08:34 | 42.2 | 31 | 2 | 24.8 | 1021 | 164.06 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHG010MB | 2020-11-05 08:38 | 40.3 | 29.8 | 2.7 | 27.2 | 1020 | 19.97 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0035 | 2020-11-05 08:44 | 55.8 | 37.8 | 0.9 | 5.5 | 1020 | 1.12 | 0 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0036 | 2020-11-05 08:46 | 34.9 | 26.7 | 0.4 | 38 | 1020 | -2.11 | 0 | 0 | LOW | partially open | vacuum decreased |  | 4
BHGV0036 | 2020-11-05 08:46 | 34.7 | 26.9 | 0.1 | 38.3 | 1020 | 1.18 | 0 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0037 | 2020-11-05 08:47 | 57.2 | 28.7 | 0.7 | 13.4 | 1021 | -0.86 | 0 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0037 | 2020-11-05 08:48 | 56.6 | 28.5 | 1 | 13.9 | 1021 | -0.6 | 1 | 0 | LOW | partially open | no vacuum change |  | 1
BHM010MB | 2020-11-05 08:51 | 48.1 | 36.3 | 0.1 | 15.5 | 1021 | -12.83 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0018 | 2020-11-05 08:52 | 54.9 | 39.4 | 0 | 5.7 | 1020 | -12.8 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHLC004B | 2020-11-05 08:54 | 0.4 | 4.8 | 18.5 | 76.3 | 1021 | -11.61 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHR0004B | 2020-11-05 08:56 | 54.6 | 36.7 | 1 | 7.7 | 1020 | -12.56 | 2 | 0 | LOW | partially open | vacuum increased |  | 1
BHR0004B | 2020-11-05 08:56 | 54.6 | 36.7 | 1.1 | 7.6 | 1020 | 0.28 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0015 | 2020-11-05 08:59 | 56.5 | 39.3 | 0.9 | 3.3 | 1020 | -13.04 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0014 | 2020-11-05 09:03 | 54.3 | 38.2 | 0 | 7.5 | 1021 | -12.88 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0013 | 2020-11-05 09:08 | 5.6 | 6.9 | 16.3 | 71.2 | 1021 | 2.63 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0016 | 2020-11-05 09:11 | 38.9 | 32.5 | 0.1 | 28.5 | 1021 | -12.68 | 1 | 0 | LOW | fully open | vacuum decreased |  | 4
BHGV0016 | 2020-11-05 09:11 | 38.5 | 33.1 | 0.3 | 28.1 | 1021 | 0.3 | 1 | 0 | LOW | partially open | no vacuum change |  | 4
BHM010MA | 2020-11-05 09:14 | 48 | 36.4 | 0.1 | 15.5 | 1021 | -13.52 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHL000C4 | 2020-11-05 09:16 | 0.2 | 3.4 | 18.8 | 77.6 | 1021 | -0.67 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0017 | 2020-11-05 09:18 | 27.8 | 23.2 | 2.1 | 46.9 | 1020 | -12.79 | 3 | 0 | LOW | partially open | vacuum decreased |  | 4
BHGV0017 | 2020-11-05 09:18 | 27.7 | 24.2 | 1.6 | 46.5 | 1020 | 0.25 | 3 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0038 | 2020-11-05 09:20 | 0.4 | 3.1 | 18.9 | 77.6 | 1020 | -2.94 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0039 | 2020-11-05 09:21 | 58.4 | 29.1 | 0.6 | 11.9 | 1021 | -13.62 | 1 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0039 | 2020-11-05 09:21 | 56.8 | 30.1 | 0.3 | 12.8 | 1021 | 0.24 | 1 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0011 | 2020-11-05 09:23 | 43.6 | 25.6 | 0.6 | 30.2 | 1022 | -6.56 | 0 | 0 | LOW | partially open | vacuum decreased |  | 4
BHGV0011 | 2020-11-05 09:23 | 43.7 | 26.4 | 0.3 | 29.6 | 1022 | 0.31 | 0 | 0 | LOW | partially open | no vacuum change |  | 4
BHGV0040 | 2020-11-05 09:25 | 39 | 28.8 | 0.1 | 32.1 | 1021 | -13.2 | 1 | 0 | LOW | partially open | vacuum decreased |  | 4
BHGV0040 | 2020-11-05 09:25 | 38.9 | 28.8 | 0.4 | 31.9 | 1021 | 0.35 | 1 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0009 | 2020-11-05 09:27 | 40.5 | 28.3 | 0.1 | 31.1 | 1022 | -4.42 | 2 | 0 | LOW | closed | no vacuum change |  | 6
BHGV0041 | 2020-11-05 09:31 | 49.7 | 34.1 | 0.2 | 16 | 1021 | -12.99 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0046 | 2020-11-05 09:33 | 48 | 35.5 | 0.3 | 16.2 | 1020 | -7.93 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0042 | 2020-11-05 09:38 | 1.4 | 4.1 | 18.1 | 76.4 | 1020 | -2.24 | 0 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0043 | 2020-11-05 09:42 | 44.4 | 30 | 1.9 | 23.7 | 1021 | -4.16 | 0 | 0 | LOW | partially open | no vacuum change |  | 4
BHGV0007 | 2020-11-05 09:43 | 28.9 | 26.1 | 0.5 | 44.5 | 1021 | -7.28 | 0 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0008 | 2020-11-05 09:44 | 7 | 9.2 | 14.8 | 69 | 1021 | -2.35 | 7 | 0 | LOW | closed | no vacuum change |  | 2
BHLC002R | 2020-11-05 09:46 | 42.1 | 31.1 | 0 | 26.8 | 1021 | -14.01 | 0 | 0 | LOW | fully open | vacuum decreased |  | 4
BHLC002R | 2020-11-05 09:46 | 41.7 | 31.2 | 0 | 27.1 | 1021 | 0.25 | 0 | 0 | LOW | partially open | no vacuum change |  | 4
BHGV0044 | 2020-11-05 09:47 | 11.2 | 21.6 | 2.1 | 65.1 | 1021 | -0.17 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0004 | 2020-11-05 09:58 | 25 | 21.6 | 3.7 | 49.7 | 1021 | -1.13 | 0 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0003 | 2020-11-05 09:59 | 69.7 | 32 | 0.3 | 0 | 1021 | -15.2 | 0 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0006 | 2020-11-05 10:02 | 35.1 | 20.5 | 8 | 36.4 | 1021 | -2.64 | 3 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0045 | 2020-11-05 10:08 | 47.5 | 29.9 | 1.2 | 21.4 | 1021 | -15.31 | 0 | 0 | LOW | fully open | no vacuum change |  | 4
BHR00001 | 2020-11-05 10:10 | 47.4 | 29.1 | 0 | 23.5 | 1021 | -15.21 | 0 | 0 | LOW | fully open | no vacuum change |  | 4
BHR0001B | 2020-11-05 10:12 | 66.8 | 32.8 | 0.2 | 0.2 | 1021 | 6.96 | 1 | 0 | LOW | vacuum increased | no vacuum change |  | 1
BHR0001B | 2020-11-05 10:12 | 66.8 | 33.2 | 0.2 | 0 | 1021 | -15.17 | 1 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0026 | 2020-11-05 10:16 | 44.4 | 31.7 | 0.3 | 23.6 | 1020 | -4.66 | 1 | 0 | LOW | fully open | no vacuum change |  | 4
BHGV000A | 2020-11-05 10:19 | 60.1 | 39.5 | 0 | 0.4 | 1020 | -5.84 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHR0002B | 2020-11-05 10:22 | 0.5 | 8.6 | 16 | 74.9 | 1020 | 1.35 | 1 | 0 | LOW | closed | no vacuum change |  | 8
BHGV0027 | 2020-11-05 10:30 | 60.5 | 40.2 | 0 | 0 | 1020 | -3.68 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0025 | 2020-11-05 10:33 | 32.8 | 23.6 | 4.7 | 38.9 | 1020 | -1.72 | 0 | 0 | LOW | closed | no vacuum change |  | 6
BHGV0024 | 2020-11-05 10:35 | 62.9 | 37.1 | 0 | 0 | 1021 | -3.03 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0048 | 2020-11-05 10:46 | 52.3 | 36.8 | 0 | 10.9 | 1021 | -4.82 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0028 | 2020-11-05 10:48 | 58.2 | 35.9 | 0.4 | 5.5 | 1021 | -4.8 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0029 | 2020-11-05 10:50 | 57.5 | 37.5 | 0.1 | 4.9 | 1020 | -4.83 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0031 | 2020-11-05 10:54 | 47.2 | 32.9 | 0.5 | 19.4 | 1020 | -12.88 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHLC0005 | 2020-11-05 10:56 | 16.6 | 12 | 14.1 | 57.3 | 1020 | -0.07 | 0 | 0 | LOW | partially open | vacuum increased |  | 4
BHLC0005 | 2020-11-05 10:56 | 16.4 | 12.2 | 14.1 | 57.3 | 1020 | 0.5 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHLC006B | 2020-11-05 10:58 | 49.4 | 32.4 | 0.5 | 17.7 | 1020 | -13.41 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHR0006B | 2020-11-05 10:59 | 0.4 | 5.8 | 17.6 | 76.2 | 1020 | 2.04 | 3 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0033 | 2020-11-05 11:01 | 38.9 | 23.2 | 7.3 | 30.6 | 1020 | -4.02 | 1 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0032 | 2020-11-05 11:02 | 59.8 | 40.1 | 0.2 | 0 | 1020 | -1.91 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0049 | 2020-11-05 11:04 | 25.2 | 22.3 | 0.8 | 51.7 | 1020 | -6.18 | 0 | 0 | LOW | closed | no vacuum change |  | 4
BHLC0006 | 2020-11-05 11:06 | 17.5 | 10.4 | 13.7 | 58.4 | 1020 | 1.86 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0022 | 2020-11-05 11:07 | 78.1 | 23.3 | 1.2 | 0 | 1021 | 14.59 | 0 | 0 | LOW | fully open | no vacuum change |  | 7
BHG010MA | 2020-11-05 11:13 | 44.5 | 31 | 1.4 | 23.1 | 1021 | -17.42 | 1 | 0 | LOW | fully open | no vacuum change |  | 1
BHG01MDA | 2020-11-05 11:17 | 45.9 | 32.8 | 0.7 | 20.6 | 1021 | 169.44 | 1 | 0 | LOW | fully open | no vacuum change |  | 1

## December 2020
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-12-02
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 999 | 0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.3 | 19.1 | 79.6 | 0 | 0 | 999 | -0.03 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.5 | 3.1 | 13.5 | 79.9 | 0 | 0 | 999 | -0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.2 | 5.5 | 15.9 | 75.4 | 0 | 0 | 999 | -0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.4 | 17.2 | 81.4 | 0 | 0 | 999 | -0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1 | 17.8 | 81.2 | 0 | 0 | 999 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.6 | 17 | 82.4 | 0 | 0 | 999 | 0.05 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.2 | 19.3 | 80.5 | 0 | 0 | 999 | 0.03 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.7 | 19.2 | 80.1 | 0 | 0 | 999 | -0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.2 | 19.6 | 79.2 | 0 | 0 | 999 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.6 | 19.1 | 80.3 | 0 | 0 | 998 | -0.04 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 15.4 | 83.2 | 0 | 0 | 999 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.3 | 17.2 | 82.5 | 0 | 0 | 998 | -0.02 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.6 | 17.5 | 80.9 | 0 | 0 | 999 | -0.11 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.4 | 19.2 | 80.4 | 0 | 0 | 998 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.6 | 19 | 79.4 | 0 | 0 | 999 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-12-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.9 | 19.1 | 80 | 0 | 0 | 1007 | 0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.1 | 19.2 | 79.7 | 0 | 0 | 1007 | -0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4 | 3.4 | 13.7 | 72.2 | 0 | 0 | 1008 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 2.8 | 5.9 | 15.1 | 76.2 | 0 | 0 | 1008 | -0.16 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 17.5 | 81.2 | 0 | 0 | 1008 | -0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 17.2 | 81.7 | 0 | 0 | 1007 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.9 | 16.8 | 81.3 | 0 | 0 | 1008 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.9 | 19 | 80.1 | 0 | 0 | 1008 | 0.08 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 19.4 | 80 | 0 | 0 | 1007 | -0.03 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.1 | 19.2 | 79.7 | 0 | 0 | 1008 | -0.09 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.8 | 19.3 | 79.9 | 0 | 0 | 1008 | -0.05 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.6 | 15.2 | 83.2 | 0 | 0 | 1008 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.4 | 17 | 82.6 | 0 | 0 | 1008 | -0.02 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 17.3 | 80.8 | 0 | 0 | 1008 | -0.17 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 1008 | -0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.9 | 18.8 | 79.3 | 0 | 0 | 1008 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-12-16
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.2 | 19.3 | 79.5 | 0 | 0 | 998 | -0.16 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.6 | 18.9 | 79.5 | 0 | 0 | 999 | 0.13 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.9 | 3.2 | 12.9 | 71.1 | 0 | 0 | 997 | 0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 4.4 | 6.8 | 14.3 | 74.5 | 0 | 0 | 998 | -0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.3 | 17.4 | 81.3 | 0 | 0 | 998 | -0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.2 | 17.1 | 81.7 | 0 | 0 | 998 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.6 | 17.4 | 81 | 0 | 0 | 998 | -0.09 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.8 | 19.4 | 79.8 | 0 | 0 | 997 | -0.02 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 19.1 | 80 | 0 | 0 | 998 | -0.13 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.5 | 19 | 79.5 | 0 | 0 | 998 | -0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.9 | 19.4 | 79.7 | 0 | 0 | 998 | -0.07 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.4 | 16.9 | 81.7 | 0 | 0 | 998 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.4 | 17 | 82.6 | 0 | 0 | 998 | 0.01 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.6 | 18.6 | 79.8 | 0 | 0 | 998 | -0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.8 | 19.1 | 80.1 | 0 | 0 | 998 | -0.14 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 19 | 78.9 | 0 | 0 | 998 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-12-22
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1002 | 0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | Flooded | [7 empty] | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 1.5 | 19.2 | 79.3 | 0 | 0 | 1002 | -0.05 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 3.6 | 3.2 | 13.6 | 79.6 | 0 | 0 | 1002 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.4 | 5.3 | 15.5 | 75.8 | 0 | 0 | 1002 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1.5 | 17 | 81.5 | 0 | 0 | 1002 | -0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 17.3 | 81.6 | 0 | 0 | 1002 | -0.06 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.7 | 17.3 | 82 | 0 | 0 | 1002 | 0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 0.3 | 19.2 | 80.5 | 0 | 0 | 1002 | 0.04 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.6 | 19.3 | 80.1 | 0 | 0 | 1002 | -0.06 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.3 | 19.5 | 79.2 | 0 | 0 | 1002 | -0.1 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.5 | 19.2 | 80.3 | 0 | 0 | 1002 | -0.12 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 1.5 | 15.5 | 83 | 0 | 0 | 1002 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | 0 | 0.2 | 17.3 | 82.5 | 0 | 0 | 1002 | -0.04 | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.5 | 17.9 | 80.6 | 0 | 0 | 1002 | -0.13 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 19 | 80.7 | 0 | 0 | 1002 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.5 | 19.3 | 79.2 | 0 | 0 | 1002 | 0 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2020-12-31
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | PC(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 19.2 | 80.6 | 0 | 0 | 987 | 0.39 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 1.7 | 18.3 | 79.9 | 0 | 0 | 988 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 0.1 | 0.4 | 18.8 | 80.7 | 0 | 0 | 987 | 0.24 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.4 | 5.1 | 14.4 | 68.1 | 0 | 0 | 987 | -0.01 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Flooded | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 17.4 | 81.5 | 0 | 0 | 987 | -0.04 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.5 | 19 | 80.4 | 0 | 0 | 987 | 0 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 19.1 | 80.8 | 0 | 0 | 987 | -0.59 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.2 | 18.8 | 80.9 | 0 | 0 | 987 | -0.85 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0 | 0.8 | 19.2 | 80 | 0 | 0 | 987 | -0.06 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 0.2 | 18.5 | 81.2 | 0 | 0 | 986 | 0.6 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0.1 | 5.3 | 15.5 | 79.1 | 0 | 0 | 986 | 0 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 19.2 | 80.6 | 0 | 0 | 986 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2 | 19.1 | 78.9 | 0 | 0 | 986 | -0.06 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA10078 | MCERTS certified instrument
Date downloaded | 2020-12-01 19:22 | Software Version | 1.10.0
Computer & User Info | YLEMYLR-BC4T | paul.carroll
Date of last user calibration | N/A
Date of last factory calibration | 2020-11-10
Next service due | 2021-05-11
Date of last Gas Check | 2020-11-10
Security code | [43632B70]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | H2 | CHOSEN 1 | CHOSEN 2 | ANSWER 1 | ANSWER 2
|  | % | % | % | % | mb | mb | ppm | ppm | ppm
BHG010MB | 2020-12-01 13:14 | 57.1 | 42.2 | 0.3 | 0 | 1006 | -18.24 | 2 | 0 | LOW | fully open | vacuum increased |  | 1
BHG01MDB | 2020-12-01 13:16 | 57.6 | 43.6 | 0.2 | 0 | 1006 | 219.76 | 3 | 0 | LOW | fully open | vacuum increased |  | 1
BHGV0035 | 2020-12-01 13:19 | 58 | 41.9 | 0.1 | 0 | 1006 | 4.04 | 1 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0037 | 2020-12-01 13:23 | 62.4 | 42.1 | 0 | 0 | 1007 | 1.97 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHM010MB | 2020-12-01 13:24 | 58.8 | 43.8 | 0.1 | 0 | 1007 | -11.59 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0018 | 2020-12-01 13:27 | 59 | 45.1 | 0 | 0 | 1007 | -11.88 | 4 | 0 | LOW | fully open | no vacuum change |  | 1
BHLC004B | 2020-12-01 13:31 | 0.3 | 2.6 | 20.3 | 76.8 | 1007 | -2.03 | 1 | 0 | LOW | closed | no vacuum change |  | 2
BHR0004B | 2020-12-01 13:33 | 58.2 | 41.9 | 0.9 | 0 | 1007 | -12.65 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0015 | 2020-12-01 13:34 | 59 | 43.2 | 0.7 | 0 | 1007 | -12.67 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0014 | 2020-12-01 13:35 | 58.4 | 41.1 | 0.8 | 0 | 1007 | -12.33 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0013 | 2020-12-01 13:36 | 1 | 7.8 | 12.6 | 78.6 | 1007 | 0.27 | 1 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0016 | 2020-12-01 13:37 | 59.9 | 42.7 | 0.5 | 0 | 500 | -12.79 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHM010MA | 2020-12-01 13:39 | 58.8 | 43 | 0.3 | 0 | 1007 | -13.25 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHL000C4 | 2020-12-01 13:41 | 61 | 40.3 | 0 | 0 | 1007 | 0.53 | 2 | 0 | LOW | closed | vacuum increased |  | 1
BHL000C4 | 2020-12-01 13:41 | 61 | 40.3 | 0.2 | 0 | 1007 | 0 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0017 | 2020-12-01 13:42 | 38.4 | 27.9 | 7.3 | 26.4 | 1007 | -12.89 | 2 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0038 | 2020-12-01 13:44 | 62 | 34.2 | 0.1 | 3.7 | 1007 | 3.83 | 3 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0038 | 2020-12-01 13:44 | 62.2 | 34.5 | 0 | 3.3 | 1007 | -0.08 | 3 | 0 | LOW | partially open | vacuum decreased |  | 1
BHGV0039 | 2020-12-01 13:46 | 59.9 | 43.1 | 0.2 | 0 | 1007 | -12.14 | 3 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0039 | 2020-12-01 13:46 | 59.8 | 43.2 | 0.2 | 0 | 1007 | -0.05 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0011 | 2020-12-01 13:47 | 66 | 37.1 | 0.8 | 0 | 1008 | 2.39 | 2 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0011 | 2020-12-01 13:47 | 68.5 | 38.9 | 0.2 | 0 | 1008 | -0.05 | 2 | 0 | LOW | fully open | vacuum increased |  | 1
BHGV0040 | 2020-12-01 13:50 | 66 | 38.1 | 0 | 0 | 1008 | 0.22 | 3 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0040 | 2020-12-01 13:50 | 65.6 | 38.4 | 0 | 0 | 1008 | 0.01 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0009 | 2020-12-01 13:52 | 65.1 | 36.3 | 0 | 0 | 1008 | 3.25 | 4 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0009 | 2020-12-01 13:52 | 65.7 | 36.6 | 0.1 | 0 | 1008 | 0.04 | 4 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0041 | 2020-12-01 13:54 | 59.5 | 40.9 | 0.3 | 0 | 1006 | -7.76 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0046 | 2020-12-01 13:55 | 60.1 | 41.7 | 0.8 | 0 | 1006 | 2.14 | 3 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0046 | 2020-12-01 13:56 | 60.2 | 41.8 | 0.2 | 0 | 1006 | -39.35 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0043 | 2020-12-01 13:59 | 62.5 | 38 | 0.3 | 0 | 1007 | 3.81 | 3 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0043 | 2020-12-01 13:59 | 62.7 | 38.2 | 0.1 | 0 | 1007 | 0 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0007 | 2020-12-01 14:00 | 66.6 | 36.1 | 0.1 | 0 | 1007 | 0.41 | 2 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0007 | 2020-12-01 14:00 | 66.1 | 36.3 | 0 | 0 | 1007 | 0.07 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0008 | 2020-12-01 14:02 | 2.5 | 4.5 | 18.7 | 74.3 | 1007 | -3.25 | 4 | 0 | LOW | closed | no vacuum change |  | 2
BHLC002R | 2020-12-01 14:06 | 46.9 | 33.6 | 1.7 | 17.8 | 1008 | 1.2 | 0 | 0 | LOW | partially open | no vacuum change |  | 4
BHGV0044 | 2020-12-01 14:07 | 43.7 | 29.3 | 1.8 | 25.2 | 1007 | 0.03 | 1 | 0 | LOW | closed | vacuum increased |  | 4
BHGV0044 | 2020-12-01 14:08 | 45.9 | 30.2 | 0.8 | 23.1 | 1007 | 0.12 | 2 | 0 | LOW | partially open | no vacuum change |  | 4
BHGV0004 | 2020-12-01 14:13 | 34.1 | 25.7 | 2 | 38.2 | 1008 | 2.3 | 1 | 0 | LOW | closed | no vacuum change |  | 4
BHLC002B | 2020-12-01 14:14 | 30.7 | 22.7 | 8.1 | 38.5 | 1008 | 0.34 | 3 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0045 | 2020-12-01 14:17 | 64.6 | 37.4 | 0.7 | 0 | 1008 | 0.65 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0001 | 2020-12-01 14:19 | 65.3 | 36.8 | 0.9 | 0 | 1008 | 1.21 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHR00001 | 2020-12-01 14:23 | 63.8 | 36.2 | 1.6 | 0 | 1007 | 3.54 | 2 | 0 | LOW | partially open | vacuum increased |  | 1
BHR00001 | 2020-12-01 14:23 | 63.1 | 36.2 | 1.8 | 0 | 1007 | 0.19 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0026 | 2020-12-01 14:27 | 61.5 | 41.9 | 0.1 | 0 | 1006 | 5.19 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV000A | 2020-12-01 14:32 | 59.9 | 43.1 | 0.1 | 0 | 1006 | 1.83 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0027 | 2020-12-01 14:38 | 59.4 | 43.5 | 0.5 | 0 | 1006 | 3.63 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0025 | 2020-12-01 14:41 | 40.6 | 33.1 | 0.1 | 26.2 | 1007 | 4.97 | 2 | 0 | LOW | closed | no vacuum change |  | 4
BHGV0024 | 2020-12-01 14:43 | 58.8 | 43.9 | 0 | 0 | 1007 | -0.11 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0023 | 2020-12-01 14:45 | 0.3 | 4.7 | 17.6 | 77.4 | 1007 | 0.48 | 0 | 0 | LOW | closed | vacuum increased |  | 1
BHGV0023 | 2020-12-01 14:45 | 0.4 | 4.7 | 17.6 | 77.3 | 1007 | 0.23 | 0 | 0 | LOW | closed | no vacuum change |  | 2
BHGV0028 | 2020-12-01 14:49 | 59.1 | 43.6 | 0.2 | 0 | 1006 | 3.16 | 4 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0029 | 2020-12-01 14:51 | 60.5 | 42.5 | 0.1 | 0 | 1006 | 3.18 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV000C | 2020-12-01 14:53 | 60.8 | 42.5 | 0.6 | 0 | 1006 | 1.91 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0031 | 2020-12-01 14:57 | 60.8 | 39.9 | 0.8 | 0 | 1006 | -11.16 | 2 | 0 | LOW | fully open | no vacuum change |  | 1
BHLC0005 | 2020-12-01 14:59 | 59.7 | 43.1 | 0.2 | 0 | 1006 | 1.17 | 3 | 1 | LOW | closed | vacuum increased |  | 1
BHLC0005 | 2020-12-01 14:59 | 59.8 | 43.2 | 0.1 | 0 | 1006 | 0.03 | 3 | 1 | LOW | partially open | no vacuum change |  | 1
BHLC006B | 2020-12-01 15:01 | 56.7 | 41.1 | 0 | 2.2 | 1006 | -11.29 | 3 | 0 | LOW | fully open | no vacuum change |  | 1
BHLC0005 | 2020-12-01 15:03 | 45.1 | 34.4 | 4.1 | 16.4 | 1006 | 9.05 | 4 | 0 | LOW | closed | no vacuum change |  | 4
BHLC0006 | 2020-12-01 15:04 | 62.3 | 38.5 | 0.2 | 0 | 1006 | 0.5 | 3 | 0 | LOW | closed | vacuum increased |  | 1
BHLC0006 | 2020-12-01 15:04 | 54.4 | 38.8 | 0 | 6.8 | 1006 | 0.14 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHGV0033 | 2020-12-01 15:06 | 60 | 42.4 | 0.6 | 0 | 1006 | 2.19 | 3 | 0 | LOW | partially open | vacuum increased |  | 1
BHGV0033 | 2020-12-01 15:06 | 59.8 | 42.5 | 0.2 | 0 | 1006 | 0.1 | 3 | 0 | LOW | partially open | no vacuum change |  | 1
BHR0006B | 2020-12-01 15:08 | 58.3 | 44.8 | 0 | 0 | 1006 | 2.63 | 4 | 0 | LOW | fully open | no vacuum change |  | 1
BHGV0049 | 2020-12-01 15:10 | 61.5 | 41.8 | 0.3 | 0 | 1006 | 2.04 | 2 | 0 | LOW | closed | vacuum increased |  | 4
BHGV0049 | 2020-12-01 15:10 | 60.8 | 41.8 | 0.1 | 0 | 1006 | 0.14 | 2 | 0 | LOW | partially open | no vacuum change |  | 1
BHG01MDB | 2020-12-01 15:13 | 57.5 | 39.5 | 0.5 | 2.5 | 1007 | 200.94 | 3 | 0 | LOW | fully open | vacuum increased |  | 1
BHG010MA | 2020-12-01 15:14 | 57.3 | 39.9 | 1.7 | 1.1 | 1007 | -21.33 | 3 | 0 | LOW | fully open | no vacuum change |  | 1

## January 2021
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-01-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 18.6 | 81.1 | 0 | 0 | 1001 | 0.22 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 1002 | 0.16 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 1002 | 0.18 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 12.2 | 3.4 | 13.8 | 65.1 | 0 | 0 | 1001 | 0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.6 | 3 | 12.5 | 74.9 | 0 | 0 | 1001 | 0.17 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Flooded | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.1 | 17.4 | 81.5 | 0 | 0 | 1001 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3 | 18.1 | 78.8 | 0 | 0 | 1001 | 0.61 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1001 | 0.12 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.3 | 18.1 | 81.6 | 0 | 0 | 1001 | 0.11 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 18.2 | 81.4 | 0 | 0 | 1001 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.1 | 18.2 | 81.7 | 0 | 0 | 1000 | 0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.2 | 16.1 | 78.7 | 0 | 0 | 1000 | 0.23 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 1000 | 0.26 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-01-14
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18.7 | 81.1 | 0 | 0 | 1000 | 0.19 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0 | 18.4 | 81.6 | 0 | 0 | 1000 | 0.13 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.3 | 18.2 | 81.5 | 0 | 0 | 1001 | 0.13 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 11.9 | 3.3 | 13.9 | 70.9 | 0 | 0 | 1000 | 0.12 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.2 | 3.2 | 12.7 | 74.9 | 0 | 0 | 1000 | 0.04 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Flooded | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 17.5 | 81.1 | 0 | 0 | 1000 | -0.03 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3 | 18.4 | 78.6 | 0 | 0 | 1001 | 0.55 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1001 | 0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 1000 | 0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.3 | 18.5 | 81.1 | 0 | 0 | 1001 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.2 | 18.4 | 81.4 | 0 | 0 | 1000 | 0.06 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.9 | 16.3 | 78.8 | 0 | 0 | 1000 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.3 | 18.3 | 81.4 | 0 | 0 | 1000 | 0.24 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-01-21
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 18.3 | 81.6 | 0 | 0 | 965 | -0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.4 | 18 | 81.6 | 0 | 0 | 965 | -0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 4.6 | 2.8 | 14.5 | 78.1 | 0 | 0 | 965 | -0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 3.8 | 2.6 | 16.9 | 76.7 | 0 | 0 | 965 | 0 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Flooded | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.2 | 17.3 | 81.5 | 0 | 0 | 965 | -0.02 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.4 | 17.8 | 80.8 | 0 | 0 | 965 | 0.57 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 964 | 0.01 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0 | 18 | 82 | 0 | 0 | 965 | 0 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 18.4 | 81.3 | 0 | 0 | 964 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.8 | 16.9 | 81.2 | 0 | 0 | 964 | 0.22 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.7 | 14.2 | 80.1 | 0 | 0 | 965 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 19.5 | 80.4 | 0 | 0 | 965 | -0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-01-28
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 18.1 | 81.8 | 0 | 0 | 982 | 0.14 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 0.6 | 17.6 | 81.7 | 0 | 0 | 983 | 0.1 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 2.9 | 2.3 | 14.6 | 80.2 | 0 | 0 | 982 | 0.07 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 11.1 | 6.8 | 14.4 | 67.7 | 0 | 0 | 982 | 0.37 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | Flooded | [7 empty] | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.5 | 13.8 | 84.7 | 0 | 0 | 982 | 0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 17.7 | 81.5 | 0 | 0 | 983 | 0.27 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 18.1 | 81.9 | 0 | 0 | 982 | -0.33 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 982 | -0.68 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 18.2 | 81.5 | 0 | 0 | 982 | -0.03 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 2.5 | 15 | 82.4 | 0 | 0 | 981 | 0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | Buried | [7 empty] | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.6 | 14.8 | 81.6 | 0 | 0 | 982 | 0.14 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 18.2 | 81.8 | 0 | 0 | 982 | 0.12 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Model | GA2000Plus | Serial No | GA12849 | MCERTS certified instrument
Date downloaded | 2021-01-28 17:56 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2021-01-18
Date of last factory calibration | 2020-08-28
Next service due | 2021-02-28
Date of last Gas Check | 2020-08-28
Security code | [0EFF95E1]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | mb | mb | ppm | ppm
BHG010MA | 2021-01-28 11:05 | 50 | 36.5 | 0.4 | 13.1 | 982 | -18.63 | 1 | 0
BHG01MDA | 2021-01-28 11:26 | 47.4 | 34.8 | 0.5 | 17.3 | 982 | 166.02 | 0 | 0
BHGV0035 | 2021-01-28 11:36 |  |  |  |  | 982 | 1.38 | 0 | 0
BHGV0036 | 2021-01-28 11:40 | 62.6 | 32.6 | 0 | 4.8 | 982 | 0.1 | 0 | 0
BHGV0036 | 2021-01-28 11:41 | 63 | 31.9 | 0 | 5.1 | 982 | -1.16 | 0 | 0
BHGV0037 | 2021-01-28 11:43 | 70.4 | 33.5 | 0 | 0 | 982 | 0.14 | 0 | 0
BHGV0037 | 2021-01-28 11:44 | 69.9 | 33.8 | 0 | 0 | 982 | -0.71 | 0 | 0
BHM010MB | 2021-01-28 11:46 | 43.6 | 35.7 | 0 | 20.7 | 982 | -18.64 | 0 | 0
BHGV0018 | 2021-01-28 11:49 | 54.4 | 38.3 | 0.5 | 6.8 | 983 | -18.36 | 2 | 0
BHLC004B | 2021-01-28 11:51 | 33.5 | 24.2 | 7 | 35.3 | 983 | -0.4 | 1 | 0
BHR0004B | 2021-01-28 11:52 | 41.2 | 31.4 | 0.6 | 26.8 | 983 | -19.08 | 1 | 0
BHR0004B | 2021-01-28 11:52 | 41.2 | 32.8 | 0.2 | 25.8 | 983 | -19.35 | 0 | 0
BHGV0015 | 2021-01-28 11:53 | 59.4 | 35.4 | 0.4 | 4.8 | 983 | -18.71 | 0 | 0
BHGV0014 | 2021-01-28 11:54 | 42.5 | 36.5 | 0.1 | 20.9 | 983 | -18.9 | 1 | 0
BHGV0014 | 2021-01-28 11:54 | 42.4 | 35.9 | 0.1 | 21.6 | 983 | -5.55 | 0 | 0
BHGV0013 | 2021-01-28 11:55 | 5.4 | 15 | 10.6 | 69 | 983 | -0.01 | 0 | 0
BHGV0016 | 2021-01-28 11:56 | 36.8 | 29 | 0.6 | 33.6 | 983 | -14.52 | 0 | 0
BHGV0016 | 2021-01-28 11:57 | 36.7 | 29.8 | 0.2 | 33.3 | 983 | -6.85 | 0 | 0
BHM010MA | 2021-01-28 11:58 | 52.1 | 39.3 | 0 | 8.6 | 983 | -20.77 | 1 | 0
BHL000C4 | 2021-01-28 12:00 | 50.6 | 32.8 | 0 | 16.6 | 982 | -0.13 | 1 | 0
BHL000C4 | 2021-01-28 12:02 | 51 | 31.4 | 0.3 | 17.3 | 982 | -1.69 | 0 | 0
BHGV0038 | 2021-01-28 12:03 | 71.5 | 27.6 | 0.4 | 0.5 | 982 | -0.71 | 2 | 0
BHGV0038 | 2021-01-28 12:04 | 72.6 | 25.2 | 0.2 | 2 | 982 | -1.84 | 3 | 0
BHGV0039 | 2021-01-28 12:06 | 51.7 | 27.9 | 0.4 | 20 | 983 | -22.03 | 0 | 0
BHGV0011 | 2021-01-28 12:09 | 49.2 | 24.4 | 0 | 26.4 | 983 | -0.95 | 0 | 0
BHGV0011 | 2021-01-28 12:10 | 48.6 | 24.1 | 0 | 27.3 | 983 | -1.89 | 0 | 0
BHLC001B | 2021-01-28 12:25 | 7.9 | 7.4 | 13.4 | 71.3 | 983 | -3.78 | 0 | 0
BHGV0009 | 2021-01-28 12:27 | 51.9 | 24.4 | 0.9 | 22.8 | 983 | -18.98 | 0 | 0
BHGV0009 | 2021-01-28 12:27 | 50.6 | 25.7 | 0.2 | 23.5 | 983 | -21.21 | 0 | 0
BHLC0003 | 2021-01-28 12:30 | 12.2 | 13.1 | 10.2 | 64.5 | 983 | -0.47 | 0 | 0
BHGV0040 | 2021-01-28 12:32 | 64 | 31.4 | 1.4 | 3.2 | 983 | 1.59 | 0 | 0
BHGV0040 | 2021-01-28 12:33 | 64 | 32.2 | 1 | 2.8 | 983 | -5.98 | 0 | 0
BHGV0301 | 2021-01-28 12:38 | 63 | 37.6 | 0.5 | 0 | 982 | -3.12 | 0 | 0
BHGV0301 | 2021-01-28 12:40 | 58.4 | 36.9 | 1.1 | 3.6 | 982 | -2.41 | 0 | 0
BHGV0012 | 2021-01-28 12:43 | 50.4 | 36.7 | 0.6 | 12.3 | 982 | -18.15 | 0 | 0
BHR00003 | 2021-01-28 12:45 | 54.1 | 30.2 | 2.5 | 13.2 | 981 | -4.56 | 0 | 0
BHR00003 | 2021-01-28 12:45 | 54.1 | 30.1 | 2.5 | 13.3 | 981 | -18.31 | 0 | 0
BHGV0046 | 2021-01-28 12:51 | 25.7 | 20.9 | 7.4 | 46 | 981 | -1.99 | 0 | 0
BHGV0046 | 2021-01-28 12:51 | 15.2 | 16.5 | 10.5 | 57.8 | 981 | 0.2 | 0 | 0
BHGV0041 | 2021-01-28 12:52 | 49.1 | 31 | 0.5 | 19.4 | 982 | -17.38 | 0 | 0
BHGV0042 | 2021-01-28 12:57 | 52.2 | 27.1 | 1.4 | 19.3 | 983 | -0.32 | 0 | 0
BHGV0042 | 2021-01-28 12:58 | 51.9 | 27.6 | 1.4 | 19.1 | 983 | 1.28 | 0 | 0
BHGV0043 | 2021-01-28 13:01 | 69.9 | 33.6 | 0.7 | 0 | 983 | -0.82 | 0 | 0
BHGV0007 | 2021-01-28 13:08 | 82.3 | 20.7 | 0 | 0 | 982 | 0.59 | 0 | 0
BHGV0008 | 2021-01-28 13:11 | 30.1 | 14.6 | 9 | 46.3 | 982 | 1.44 | 6 | 0
BHLC002R | 2021-01-28 13:14 | 76.5 | 26.8 | 0.2 | 0 | 983 | 0.72 | 0 | 0
BHGV0044 | 2021-01-28 13:16 | 68 | 33 | 0 | 0 | 983 | 1.52 | 0 | 0
BHGV0044 | 2021-01-28 13:16 | 67.3 | 33.1 | 0 | 0 | 983 | 1.32 | 0 | 0
BHR00001 | 2021-01-28 13:21 | 67.2 | 33.7 | 0.3 | 0 | 981 | 0.19 | 0 | 0
BHGV0001 | 2021-01-28 13:22 | 67.4 | 36.8 | 0 | 0 | 981 | 1.3 | 0 | 0
BHGV0006 | 2021-01-28 13:28 | 53.3 | 29.6 | 2.7 | 14.4 | 983 | 1.32 | 2 | 0
BHGV0006 | 2021-01-28 13:31 | 53.8 | 29.7 | 2.6 | 13.9 | 983 | 1.74 | 3 | 0
BHGV0003 | 2021-01-28 13:34 | 71.4 | 32.2 | 0.2 | 0 | 982 | 1.55 | 0 | 0
BHR0001B | 2021-01-28 13:35 | 67.8 | 36.3 | 0 | 0 | 982 | 1.54 | 0 | 0
BHGV0004 | 2021-01-28 13:40 | 45.2 | 25.3 | 0.2 | 29.3 | 982 | 2.44 | 0 | 0
BHGV0004 | 2021-01-28 13:40 | 45.3 | 25.3 | 0.2 | 29.2 | 982 | 1.97 | 0 | 0
BHLC002B | 2021-01-28 13:42 | 65.4 | 36.6 | 0 | 0 | 982 | 0.07 | 0 | 0
BHLC002B | 2021-01-28 13:43 | 65.1 | 37.1 | 0 | 0 | 982 | 0.22 | 0 | 0
BHGV0045 | 2021-01-28 13:45 | 65.5 | 38.6 | 0 | 0 | 982 | 1.24 | 0 | 0
BHGV0045 | 2021-01-28 13:46 | 65.2 | 38.6 | 0 | 0 | 982 | 2.21 | 0 | 0
BHLC002B | 2021-01-28 13:47 |  |  |  |  | 981 | 0.03 | 0 | 0
BHGV0047 | 2021-01-28 13:51 | 64.9 | 30.4 | 0.7 | 4 | 981 | 0.94 | 0 | 0
BHGV0047 | 2021-01-28 13:51 | 63.3 | 32 | 0.1 | 4.6 | 981 | 0.18 | 0 | 0
BHGV0026 | 2021-01-28 13:52 | 65.7 | 33.6 | 0.3 | 0.4 | 981 | 1.5 | 0 | 0
BHR0002B | 2021-01-28 13:54 | 64.9 | 38.3 | 0.9 | 0 | 980 | -0.11 | 0 | 0
BHGV000A | 2021-01-28 13:55 | 62 | 39.7 | 0.2 | 0 | 980 | 0.01 | 0 | 0
BHGV0027 | 2021-01-28 13:57 | 61.3 | 42.3 | 0 | 0 | 980 | 0.34 | 1 | 0
BHM050MB | 2021-01-28 14:06 | 62.1 | 41.4 | 0 | 0 | 982 | -0.04 | 0 | 0
BHGV0025 | 2021-01-28 14:08 | 47.6 | 37.1 | 0.1 | 15.2 | 981 | 0.91 | 0 | 0
BHGV0024 | 2021-01-28 14:09 | 64.7 | 38.8 | 0 | 0 | 981 | -0.05 | 0 | 0
BHGV0023 | 2021-01-28 14:13 | 0.1 | 6.9 | 15.9 | 77.1 | 982 | -0.14 | 0 | 0
BHGV0022 | 2021-01-28 14:14 | 0.7 | 6.5 | 14.9 | 77.9 | 982 | 0.07 | 0 | 0
BHGV0048 | 2021-01-28 14:18 | 63.3 | 36.5 | 0.4 | 0 | 981 | 0.2 | 0 | 0
BHLC0006 | 2021-01-28 14:20 | 63.1 | 39 | 0 | 0 | 981 | -0.15 | 0 | 0
BHLC006B | 2021-01-28 14:21 | 52.5 | 37.2 | 0.1 | 10.2 | 981 | -15.32 | 0 | 0
BHLC0005 | 2021-01-28 14:22 | 30.2 | 27.2 | 6.4 | 36.2 | 980 | -0.92 | 0 | 0
BHLC0005 | 2021-01-28 14:23 | 29.9 | 26.1 | 7.2 | 36.8 | 980 | 0.13 | 0 | 0
BHGV0029 | 2021-01-28 14:24 | 63.1 | 38.9 | 0 | 0 | 980 | 0.1 | 0 | 0
BHGV000C | 2021-01-28 14:25 | 56.6 | 37.4 | 0.8 | 5.2 | 980 | -1.09 | 0 | 0
BHGV0028 | 2021-01-28 14:27 | 62.8 | 37 | 0.4 | 0 | 980 | -0.46 | 0 | 0
BHGV000B | 2021-01-28 14:29 | 58 | 37.1 | 0.4 | 4.5 | 980 | -0.32 | 0 | 0
BHGV0030 | 2021-01-28 14:40 | 50.4 | 36.8 | 0 | 12.8 | 980 | -9.73 | 0 | 0
BHGV0030 | 2021-01-28 14:40 | 50.4 | 37 | 0 | 12.6 | 980 | -11.07 | 0 | 0
BHR00005 | 2021-01-28 14:43 | 0.1 | 4.1 | 17 | 78.8 | 980 | >>>> | 0 | 0
BHGV0031 | 2021-01-28 14:45 | 42.9 | 30.4 | 0.4 | 26.3 | 980 | -14.07 | 0 | 0
BHGV0032 | 2021-01-28 14:47 | 63 | 39.8 | 0.6 | 0 | 980 | -1.03 | 0 | 0
BHGV0033 | 2021-01-28 14:50 | 40.5 | 30 | 4.3 | 25.2 | 981 | -1.32 | 1 | 0
BHGV0033 | 2021-01-28 14:51 | 39.7 | 29.7 | 4.5 | 26.1 | 981 | -4.72 | 1 | 0
BHR0006B | 2021-01-28 14:55 | 42.1 | 28.5 | 5.1 | 24.3 | 981 | 4.33 | 2 | 0
BHGV0049 | 2021-01-28 14:58 | 62.9 | 40.2 | 0 | 0 | 981 | -1.12 | 0 | 0
BHGV0049 | 2021-01-28 14:58 | 62.6 | 39.7 | 0.1 | 0 | 981 | -9.85 | 0 | 0
BHPW0005 | 2021-01-28 15:00 | 65.4 | 38.3 | 0 | 0 | 981 | -15.08 | 0 | 0
BHPW0005 | 2021-01-28 15:02 | 63.8 | 39 | 0 | 0 | 981 | -15.07 | 0 | 0
BHPW0006 | 2021-01-28 15:05 | 3.7 | 10.9 | 13.7 | 71.7 | 981 | -0.29 | 0 | 0
BHPW0004 | 2021-01-28 15:08 | 34 | 27.9 | 1.4 | 36.7 | 981 | -4.59 | 0 | 0
BHPW0003 | 2021-01-28 15:09 | 25.7 | 18.8 | 3.5 | 52 | 981 | -8.98 | 0 | 0
BHPW0002 | 2021-01-28 15:11 | 25.2 | 19.1 | 3.6 | 52.1 | 981 | -7.41 | 0 | 0
BHPW0001 | 2021-01-28 15:13 | 24.8 | 19.1 | 3.6 | 52.5 | 981 | 0.01 | 0 | 0
BHGW0034 | 2021-01-28 15:14 | 35.2 | 19.5 | 0.6 | 44.7 | 981 | 0.55 | 0 | 0
BHG010MA | 2021-01-28 15:18 | 45 | 33.4 | 1.2 | 20.4 | 981 | -21.34 | 0 | 0
BHG01MDA | 2021-01-28 15:19 | 45.4 | 33.5 | 1.1 | 20 | 981 | 166.63 | 0 | 0

## February 2021
Date | 2021-02-03
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 974 | 0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.2 | 17.2 | 80.6 | 0 | 0 | 975 | 0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 9.6 | 3.4 | 13.2 | 69.8 | 0 | 0 | 975 | 0.21 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.3 | 0.4 | 17.6 | 81.7 | 0 | 0 | 975 | 0.14 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0 | 18 | 82 | 0 | 0 | 975 | -1.26 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.8 | 13.5 | 84.6 | 0 | 0 | 975 | 0.84 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.6 | 17.6 | 81.7 | 0 | 0 | 975 | 0.16 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.7 | 82.2 | 0 | 0 | 974 | 0.76 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.3 | 17.3 | 82.3 | 0 | 0 | 974 | 0.15 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 18.2 | 81.5 | 0 | 0 | 974 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 3.3 | 11 | 5.1 | 80.6 | 0 | 0 | 974 | 0.78 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 3.7 | 10.2 | 86 | 0 | 0 | 973 | 0.22 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.7 | 15.7 | 79.6 | 0 | 0 | 974 | 0.36 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 18 | 82 | 0 | 0 | 974 | 0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-02-12
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1001 | 0.09 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2 | 17 | 81 | 0 | 0 | 1001 | 0.1 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 16.2 | 3.2 | 12.8 | 67.8 | 0 | 0 | 1001 | 0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 13.8 | 5.1 | 13.8 | 67.3 | 0 | 0 | 1001 | 0.11 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0 | 17.8 | 82.2 | 0 | 0 | 1000 | -0.12 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 1.9 | 13.3 | 84.7 | 0 | 0 | 1001 | 0.54 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.5 | 17.6 | 81.8 | 0 | 0 | 1001 | 0.12 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 17.7 | 82.2 | 0 | 0 | 1001 | 0.45 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.1 | 17.2 | 82.6 | 0 | 0 | 1000 | 0.1 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 18.1 | 81.6 | 0 | 0 | 1000 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 2 | 13 | 4.5 | 80.5 | 0 | 0 | 1001 | 0.45 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 3.2 | 10.7 | 86 | 0 | 0 | 1001 | 0.12 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 15.7 | 79.7 | 0 | 0 | 1001 | 0.21 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 17.4 | 82.6 | 0 | 0 | 1001 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Date | 2021-02-16
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.5 | 18.8 | 79.7 | 0 | 0 | 985 | 0.59 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.7 | 18.7 | 79.6 | 0 | 0 | 987 | 1.23 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 22 | 3.2 | 7 | 62.5 | 0 | 0 | 985 | 0.65 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.2 | 10.1 | 13.3 | 62.4 | 0 | 0 | 985 | 0.57 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 1 | 16.4 | 82.6 | 0 | 0 | 986 | 0.55 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.9 | 18.2 | 79.9 | 0 | 0 | 985 | 1.12 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.4 | 19.1 | 79.5 | 0 | 0 | 985 | 8.13 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.9 | 19.2 | 79.9 | 0 | 0 | 985 | 0.53 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.3 | 19.1 | 79.6 | 0 | 0 | 984 | 0.54 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.2 | 0.3 | 18 | 81.5 | 0 | 0 | 984 | -0.01 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 1.8 | 13.2 | 5.5 | 79.5 | 0 | 0 | 984 | 0.39 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 2.1 | 18.7 | 79.2 | 0 | 0 | 984 | 0.52 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1 | 18.9 | 80.1 | 0 | 0 | 985 | 2.18 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.3 | 18.6 | 80.1 | 0 | 0 | 985 | 0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-02-23
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 8 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.1 | 18.7 | 80.2 | 0 | 0 | 995 | 0.68 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.7 | 18.5 | 79.8 | 0 | 0 | 995 | 0.63 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 27.2 | 3.2 | 1 | 51.5 | 0 | 0 | 995 | 0.53 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0.1 | 1.6 | 18.3 | 80 | 0 | 0 | 995 | 0.54 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0.1 | 1.3 | 18.3 | 80.3 | 0 | 0 | 995 | 0.64 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.8 | 18.2 | 80 | 0 | 0 | 995 | 0.94 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.7 | 18.1 | 80.2 | 0 | 0 | 995 | -3.69 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 1.2 | 18.8 | 80 | 0 | 0 | 994 | 0.39 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.8 | 18.4 | 79.8 | 0 | 0 | 994 | -0.53 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | 0.1 | 0.2 | 18.2 | 81.5 | 0 | 0 | 994 | -0.02 | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 1.6 | 13.4 | 5.2 | 79.8 | 0 | 0 | 994 | 0.35 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 3.2 | 16.7 | 80 | 0 | 0 | 994 | 0.35 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 0.6 | 19 | 80.4 | 0 | 0 | 995 | 0.62 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.2 | 18.3 | 79.8 | 0 | 0 | 994 | 0.73 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | Flooded | [7 empty] | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA12849 | MCERTS certified instrument
Date downloaded | 2021-02-23 20:08 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2021-01-18
Date of last factory calibration | 2020-08-28
Next service due | 2021-02-28
Date of last Gas Check | 2020-08-28
Security code | [89A7D8BF]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | SITECHOSEN 1 | SITECHOSEN 2 | SITECHOSEN 3 | SITECHOSEN 4
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2021-02-23 08:39 | 38.7 | 29.3 | 2.9 | 29.1 | 995 | 155.11 | 1 | 0
BHG010MB | 2021-02-23 08:54 | 35.4 | 27.7 | 3.8 | 33.1 | 994 | -21.22 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHG010MB | 2021-02-23 08:55 | 38.8 | 29.3 | 2.8 | 29.1 | 994 | 197.24 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0035 | 2021-02-23 08:57 | 38.7 | 29.3 | 3.1 | 28.9 | 994 | 0.29 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0036 | 2021-02-23 08:58 | 46.5 | 29.2 | 0.2 | 24.1 | 994 | -0.7 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0036 | 2021-02-23 08:59 | 47 | 29.2 | 0.1 | 23.7 | 994 | -1.46 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0037 | 2021-02-23 09:05 | 60 | 32.6 | 0.1 | 7.3 | 995 | 0.04 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0037 | 2021-02-23 09:06 | 59.7 | 32.5 | 0.1 | 7.7 | 995 | -8.66 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHM010MB | 2021-02-23 09:08 | 45.9 | 37.3 | 0.1 | 16.7 | 994 | -17.25 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0018 | 2021-02-23 09:11 | 46.3 | 38.3 | 0.1 | 15.3 | 995 | -17.05 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC004B | 2021-02-23 09:16 | 20.5 | 17.2 | 10.3 | 52 | 995 | 0.27 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHR0004B | 2021-02-23 09:17 | 43.1 | 34.8 | 0.3 | 21.8 | 995 | -1.7 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0015 | 2021-02-23 09:18 | 43.1 | 36.6 | 0.6 | 19.7 | 995 | -16.75 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0015 | 2021-02-23 09:19 | 43.1 | 36.8 | 0.6 | 19.5 | 995 | -16.71 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0014 | 2021-02-23 09:19 | 45.7 | 37.3 | 0.1 | 16.9 | 995 | -4.36 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0014 | 2021-02-23 09:20 | 45.6 | 37.5 | 0.1 | 16.8 | 995 | -13.91 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0013 | 2021-02-23 09:23 | 28.6 | 21.8 | 8.7 | 40.9 | 995 | 0.41 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0016 | 2021-02-23 09:24 | 55 | 38.3 | 0.8 | 5.9 | 995 | -2.32 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0016 | 2021-02-23 09:25 | 53.4 | 38.1 | 0.7 | 7.8 | 995 | -3 | 2 | 0 | drizzle | overcast | moderate wind | light wind
BHM010MA | 2021-02-23 09:29 | 45.7 | 38 | 0.1 | 16.2 | 995 | -15.84 | 3 | 0 | drizzle | overcast | moderate wind | light wind
BHL000C4 | 2021-02-23 09:30 | 32.4 | 26 | 0.4 | 41.2 | 994 | -0.71 | 11 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0038 | 2021-02-23 09:35 | 45.8 | 32.8 | 1.9 | 19.5 | 994 | -1.52 | 8 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0039 | 2021-02-23 09:41 | 36.4 | 22.6 | 3.6 | 37.4 | 995 | 0.01 | 3 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0301 | 2021-02-23 09:43 | 65.3 | 37.8 | 0.6 | 0 | 994 | -0.79 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0012 | 2021-02-23 09:50 | 46.9 | 35.2 | 0.6 | 17.3 | 994 | -16.25 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0011 | 2021-02-23 09:51 | 49.9 | 24 | 0.3 | 25.8 | 995 | -0.44 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0011 | 2021-02-23 09:52 | 50 | 23.2 | 0.1 | 26.7 | 995 | -2.6 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0040 | 2021-02-23 10:03 | 43.7 | 29.5 | 0.2 | 26.6 | 995 | -4.74 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC001B | 2021-02-23 10:05 | 1.1 | 3 | 15 | 80.9 | 995 | 0.19 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0009 | 2021-02-23 10:07 | 40.9 | 27.4 | 0.4 | 31.3 | 995 | -12.88 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHR00003 | 2021-02-23 10:18 | 62.6 | 31.6 | 2 | 3.8 | 993 | 5.45 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHR00003 | 2021-02-23 10:20 | 55.1 | 28.4 | 3 | 13.5 | 992 | -2.42 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0046 | 2021-02-23 10:23 | 0 | 1.6 | 18 | 80.4 | 992 | -0.44 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0041 | 2021-02-23 10:29 | 44.2 | 32.8 | 0.1 | 22.9 | 993 | -16.24 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0042 | 2021-02-23 10:31 | 36.6 | 19.8 | 2.7 | 40.9 | 994 | 0.36 | 7 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0043 | 2021-02-23 10:33 | 68.2 | 35.3 | 0.1 | 0 | 994 | 0.74 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0007 | 2021-02-23 10:34 | 69.4 | 32.9 | 0 | 0 | 994 | 0.94 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0008 | 2021-02-23 10:36 | 26.4 | 17.2 | 9.4 | 47 | 994 | 10.59 | 8 | 0 | drizzle | overcast | moderate wind | light wind
BHLC002R | 2021-02-23 10:38 | 67.3 | 35.5 | 0.1 | 0 | 994 | 0.72 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0044 | 2021-02-23 10:41 | 44.2 | 28.6 | 2.2 | 25 | 994 | 1.23 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0044 | 2021-02-23 10:42 | 44.6 | 28.9 | 2 | 24.5 | 994 | 0.68 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0001 | 2021-02-23 10:44 | 64.7 | 37.6 | 0.2 | 0 | 993 | 0 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHR00001 | 2021-02-23 10:47 | 69.2 | 34.6 | 0 | 0 | 993 | 0 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0006 | 2021-02-23 10:56 | 55.2 | 30.4 | 2.2 | 12.2 | 994 | 1.06 | 3 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0003 | 2021-02-23 10:57 | 71.2 | 32.7 | 0.1 | 0 | 994 | 0.68 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHR0001B | 2021-02-23 10:58 | 66.6 | 37.3 | 0 | 0 | 994 | 0.88 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0004 | 2021-02-23 10:59 | 49.9 | 25.9 | 0.2 | 24 | 994 | 0.94 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0045 | 2021-02-23 11:02 | 65.1 | 38.3 | 0 | 0 | 993 | 0.94 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0026 | 2021-02-23 11:07 | 64.4 | 39.2 | 0.4 | 0 | 993 | 0.84 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHR0002B | 2021-02-23 11:07 | 63.6 | 39.6 | 0.1 | 0 | 993 | 0.02 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV000A | 2021-02-23 11:08 | 61.4 | 41.2 | 0.1 | 0 | 993 | -0.45 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0027 | 2021-02-23 11:10 | 61.3 | 41.8 | 0.3 | 0 | 993 | -0.89 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0047 | 2021-02-23 11:11 | 57.8 | 34.7 | 0.2 | 7.3 | 994 | -0.99 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0024 | 2021-02-23 11:12 | 65.6 | 37.6 | 0.3 | 0 | 994 | -0.94 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHM050MB | 2021-02-23 11:15 | 62.9 | 38.8 | 0.3 | 0 | 994 | -0.97 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0025 | 2021-02-23 11:16 | 62.2 | 40.1 | 0.1 | 0 | 994 | 0.27 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0023 | 2021-02-23 11:18 | 61.6 | 41.3 | 0.1 | 0 | 994 | 0.06 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHM050MA | 2021-02-23 11:20 | 62.5 | 39.7 | 0 | 0 | 994 | -1.04 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0048 | 2021-02-23 11:22 | 59 | 40 | 0.2 | 0.8 | 993 | -0.88 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0022 | 2021-02-23 11:23 | 58.9 | 40.5 | 0 | 0.6 | 993 | -1.49 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC0006 | 2021-02-23 11:23 | 1.5 | 7.1 | 12.3 | 79.1 | 993 | -1.82 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC0006 | 2021-02-23 11:23 | 1.5 | 5.8 | 15.8 | 76.9 | 993 | -0.26 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC006B | 2021-02-23 11:25 | 51.3 | 36.2 | 0.6 | 11.9 | 993 | -15.73 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHLC0005 | 2021-02-23 11:26 | 22.4 | 36 | 2.5 | 39.1 | 993 | 0.24 | 2 | 1 | drizzle | overcast | moderate wind | light wind
BHGV0029 | 2021-02-23 11:28 | 61.9 | 38.9 | 0.5 | 0 | 993 | -1.01 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV000C | 2021-02-23 11:29 | 58.8 | 36.9 | 0.2 | 4.1 | 993 | -2.91 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0028 | 2021-02-23 11:30 | 61.9 | 37.1 | 0.3 | 0.7 | 993 | -1.04 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV000B | 2021-02-23 11:31 | 58.8 | 37.7 | 0.2 | 3.3 | 993 | -0.79 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0030 | 2021-02-23 11:39 | 47.1 | 34.9 | 0.5 | 17.5 | 993 | -11.56 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHR00005 | 2021-02-23 11:41 | 0 | 2.2 | 17.6 | 80.2 | 993 | 0 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0031 | 2021-02-23 11:42 | 40.2 | 32.3 | 0.5 | 27 | 993 | -13.7 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0031 | 2021-02-23 11:42 | 39.9 | 32.5 | 0.2 | 27.4 | 993 | -8.94 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0033 | 2021-02-23 11:45 | 37.2 | 28 | 5.6 | 29.2 | 993 | -0.95 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0032 | 2021-02-23 11:46 | 60.1 | 42.6 | 0.2 | 0 | 994 | -1.95 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHR0006B | 2021-02-23 11:49 | 41.5 | 28.9 | 5.1 | 24.5 | 993 | 8.02 | 3 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0049 | 2021-02-23 11:50 | 58 | 37.2 | 1.2 | 3.6 | 993 | -0.98 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGV0049 | 2021-02-23 11:51 | 56.3 | 37.4 | 0.7 | 5.6 | 993 | -2.89 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0006 | 2021-02-23 11:53 | 0.6 | 8.2 | 15.9 | 75.3 | 994 | -1.16 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0005 | 2021-02-23 11:54 | 30.5 | 25.7 | 2.3 | 41.5 | 500 | -16.33 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0004 | 2021-02-23 11:55 | 22.1 | 19.8 | 1.4 | 56.7 | 994 | -10.05 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0003 | 2021-02-23 11:56 | 6.6 | 13.9 | 4.8 | 74.7 | 994 | -14.85 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0002 | 2021-02-23 11:58 | 9.3 | 18.4 | 10.9 | 61.4 | 994 | 1.35 | 11 | 0 | drizzle | overcast | moderate wind | light wind
BHPW0001 | 2021-02-23 12:01 | 0 | 1.9 | 17.8 | 80.3 | 994 | -16.42 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHGW0034 | 2021-02-23 12:02 | 0.8 | 3.2 | 14.4 | 81.6 | 994 | 0.03 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHG010MA | 2021-02-23 12:04 | 39.5 | 28.9 | 2.7 | 28.9 | 994 | -19.34 | 0 | 0 | drizzle | overcast | moderate wind | light wind
BHG01MDA | 2021-02-23 12:06 | 45.7 | 33.7 | 0.5 | 20.1 | 995 | 192.6 | 1 | 0 | drizzle | overcast | moderate wind | light wind
BHG01MDA | 2021-02-23 12:09 | 45.7 | 34.1 | 0.2 | 20 | 995 | 160.44 | 1 | 0 | drizzle | overcast | moderate wind | light wind

## March 2021
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-03-04
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 19.5 | 80.3 | 0 | 0 | 1007 | 0.49 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1 | 18.5 | 80.5 | 0 | 0 | 1007 | 0.32 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 25.1 | 6.7 | 7.2 | 61 | 0 | 0 | 1007 | 0.47 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.1 | 8.8 | 15.2 | 60.9 | 0 | 0 | 1007 | 0.62 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 19.2 | 80.7 | 0 | 0 | 1007 | 0.6 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.4 | 18.8 | 79.8 | 0 | 0 | 1007 | 0.39 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 2.3 | 16.5 | 81.1 | 0 | 0 | 1007 | 0.82 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0 | 19.2 | 80.7 | 0 | 0 | 1007 | 0.67 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.6 | 18.7 | 80.6 | 0 | 0 | 1007 | 0.6 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 | [9 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 0.3 | 17.3 | 82.3 | 0 | 0 | 1006 | 4.53 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 2.7 | 16.5 | 80.7 | 0 | 0 | 1006 | 0.29 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.9 | 16.9 | 80.2 | 0 | 0 | 1006 | 0.34 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1.1 | 18.5 | 78.6 | 0 | 0 | 1006 | 0.34 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 4.7 | 16.3 | 79 | 0 | 0 | 1006 | 0.47 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-03-10
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 988 | 5.86 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 990 | -0.02 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.5 | 17.7 | 81.8 | 0 | 0 | 991 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.3 | 0.1 | 17.9 | 81.7 | 0 | 0 | 990 | -0.44 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 21.1 | 6 | 9.2 | 63.7 | 0 | 0 | 989 | -0.2 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.1 | 9.7 | 13 | 61.2 | 0 | 0 | 990 | -0.19 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 990 | -0.52 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 1.3 | 12.4 | 86.3 | 0 | 0 | 990 | -0.09 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.2 | 17.7 | 82 | 0 | 0 | 990 | -0.02 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | 0 | 1.9 | 16.2 | 81.9 | 0 | 0 | 990 | -0.15 | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 990 | -0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.4 | 16.3 | 82.3 | 0 | 0 | 990 | 0.24 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 1.5 | 5.4 | 1.4 | 91.7 | 0 | 0 | 989 | -0.14 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.3 | 13.8 | 85.9 | 0 | 0 | 989 | 0.6 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.7 | 17 | 82.3 | 0 | 0 | 990 | -0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 5.1 | 14.3 | 80.6 | 0 | 0 | 988 | 0.4 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 988 | -0.61 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.6 | 16.5 | 80.9 | 0 | 0 | 988 | -0.15 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-03-17
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 10 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.3 | 16.9 | 82.8 | 0 | 0 | 1021 | 0.2 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.3 | 15 | 82.7 | 0 | 0 | 1022 | -0.1 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 24.6 | 6.3 | 7.6 | 61.5 | 0 | 0 | 1021 | 0.13 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.2 | 7.1 | 13.2 | 65.5 | 0 | 0 | 1021 | -0.2 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 16.3 | 83.6 | 0 | 0 | 1022 | -0.19 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.9 | 13 | 86.1 | 0 | 0 | 1022 | 0.36 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2.5 | 16.5 | 81 | 0 | 0 | 1022 | 0.17 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1021 | -0.31 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.9 | 17.2 | 81.8 | 0 | 0 | 1021 | -0.12 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | Buried | [7 empty] | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0.1 | 17.2 | 82.7 | 0 | 0 | 1021 | -0.2 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 13.6 | 86.2 | 0 | 0 | 1021 | 0.08 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.8 | 15.4 | 83.8 | 0 | 0 | 1021 | -0.26 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.9 | 16.1 | 81 | 0 | 0 | 1020 | 0.06 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1020 | -0.43 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.1 | 17.5 | 82.4 | 0 | 0 | 1020 | -0.08 | 1 | 9.9 | 0.5 | 4.95
Date | 2021-03-23
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 11 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1008 | 0.02 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.3 | 16 | 81.7 | 0 | 0 | 1009 | 0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 17.9 | 82 | 0 | 0 | 1009 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 22.4 | 8.1 | 11.4 | 58.1 | 0 | 0 | 1009 | 0.1 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 16.6 | 9.8 | 13.3 | 60.3 | 0 | 0 | 1009 | 0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1009 | 0.07 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.6 | 9.8 | 87.6 | 0 | 0 | 1009 | 0.48 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1.7 | 17.1 | 81.2 | 0 | 0 | 1009 | -0.36 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1009 | 0.34 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.4 | 17.3 | 82.3 | 0 | 0 | 1009 | 0.08 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 6.6 | 2.8 | 13.1 | 77.5 | 0 | 0 | 1009 | 0.07 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 4 | 11.1 | 84.9 | 0 | 0 | 1009 | 0.1 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0 | 0.2 | 13.6 | 86.2 | 0 | 0 | 1009 | 0.02 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 16.9 | 82.7 | 0 | 0 | 1010 | 0.13 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.8 | 17 | 81.2 | 0 | 0 | 1008 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 18 | 81.9 | 0 | 0 | 1008 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.8 | 16.6 | 81.6 | 0 | 0 | 1008 | 0.05 | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA13202 | MCERTS certified instrument
Date downloaded | 2021-03-23 23:53 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2021-03-04
Date of last factory calibration | 2021-02-24
Next service due | 2021-08-24
Date of last Gas Check | 2021-02-24
Security code | [248C9E76]
ID | DATE | CH4 | CO2 | O2 | BALANCE | BARO | REL.PRESSURE | CO | H2S | CHOSEN 1 | CHOSEN 2
|  | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2021-03-23 09:34 | 51.6 | 34.1 | 0.5 | 13.8 | 1007 | 149.35 | 2 | 0 | fully open | no vacuum change
BHG01MDB | 2021-03-23 09:37 | 42.1 | 29.3 | 3.2 | 25.4 | 1007 | -15.29 | 3 | 0 | fully open | no vacuum change
BHG01MDB | 2021-03-23 09:45 | 51.6 | 34.3 | 0.4 | 13.7 | 1007 | 196.35 | 2 | 0 | fully open | no vacuum change
BHGV0035 | 2021-03-23 09:47 | 62.1 | 37 | 0.3 | 0.6 | 1007 | 0.61 | 2 | 0 | closed | vacuum increased
BHGV0035 | 2021-03-23 09:48 | 62 | 39.1 | 0 | 0 | 1007 | -1.02 | 1 | 0 | partially open | no vacuum change
BHGV0036 | 2021-03-23 09:50 | 62.2 | 32.9 | 0 | 4.9 | 1007 | -0.88 | 3 | 0 | closed | vacuum increased
BHGV0036 | 2021-03-23 09:50 | 62.2 | 32.8 | 0 | 5 | 1007 | -1.06 | 3 | 0 | partially open | no vacuum change
BHGV0037 | 2021-03-23 09:52 | 68.4 | 33 | 0.3 | 0 | 1007 | 0 | 2 | 0 | closed | vacuum increased
BHGV0037 | 2021-03-23 09:52 | 68.1 | 33.1 | 0.3 | 0 | 1007 | -1.1 | 2 | 0 | partially open | no vacuum change
BHM010MB | 2021-03-23 09:54 | 52.2 | 38 | 0.2 | 9.6 | 1007 | -12.82 | 3 | 0 | fully open | no vacuum change
BHGV0018 | 2021-03-23 09:56 | 52.7 | 39.3 | 0 | 8 | 1007 | -13.19 | 3 | 0 | fully open | no vacuum change
BHLC004B | 2021-03-23 09:57 | 1 | 4 | 16.2 | 78.8 | 1007 | -0.35 | 4 | 0 | closed | no vacuum change
BHR0004B | 2021-03-23 09:59 | 35.8 | 26 | 0.3 | 37.9 | 1007 | 1.92 | 2 | 0 | closed | no vacuum change
BHGV0015 | 2021-03-23 10:00 | 50.4 | 37.7 | 1.3 | 10.6 | 1007 | -13.19 | 2 | 0 | partially open | vacuum increased
BHGV0015 | 2021-03-23 10:00 | 50.2 | 37.8 | 1.4 | 10.6 | 1007 | -12.32 | 2 | 0 | partially open | no vacuum change
BHGV0014 | 2021-03-23 10:02 | 35.4 | 34.1 | 0.1 | 30.4 | 1007 | -0.01 | 2 | 0 | closed | no vacuum change
BHGV0013 | 2021-03-23 10:03 | 0.2 | 2.9 | 17.1 | 79.8 | 1007 | 0.11 | 0 | 0 | closed | no vacuum change
BHGV0016 | 2021-03-23 10:04 | 60 | 39.9 | 0.3 | 0 | 1007 | 0.23 | 2 | 0 | closed | vacuum increased
BHGV0016 | 2021-03-23 10:04 | 59.8 | 40.2 | 0.4 | 0 | 1007 | -2.63 | 2 | 0 | partially open | no vacuum change
BHM010MA | 2021-03-23 10:06 | 52.6 | 39.1 | 0.4 | 7.9 | 1007 | -12.07 | 2 | 0 | fully open | no vacuum change
BHL000C4 | 2021-03-23 10:07 | 54 | 33.7 | 0.3 | 12 | 1007 | -1.53 | 4 | 0 | closed | vacuum increased
BHL000C4 | 2021-03-23 10:08 | 55.9 | 32.1 | 0.2 | 11.8 | 1007 | -0.26 | 4 | 0 | partially open | no vacuum change
BHGV0038 | 2021-03-23 10:10 | 48.7 | 33.5 | 0.9 | 16.9 | 1006 | 0.5 | 3 | 0 | closed | vacuum increased
BHGV0038 | 2021-03-23 10:11 | 48.4 | 33.6 | 0.8 | 17.2 | 1006 | -1.95 | 3 | 0 | partially open | no vacuum change
BHGV0039 | 2021-03-23 10:12 | 61 | 32.3 | 0.9 | 5.8 | 1007 | 0.31 | 2 | 0 | closed | vacuum increased
BHGV0039 | 2021-03-23 10:13 | 61.5 | 32 | 0.9 | 5.6 | 1007 | -1.21 | 2 | 0 | partially open | no vacuum change
BHGV0011 | 2021-03-23 10:14 | 65.7 | 30.8 | 0.4 | 3.1 | 1007 | -1.45 | 1 | 0 | partially open | vacuum increased
BHGV0011 | 2021-03-23 10:14 | 66 | 29.8 | 0.1 | 4.1 | 1007 | -5.58 | 1 | 0 | partially open | no vacuum change
BHGV0010 | 2021-03-23 10:18 | 28.8 | 13.8 | 10.4 | 47 | 1008 | 7.32 | 0 | 0 | closed | no vacuum change
BHGV0040 | 2021-03-23 10:19 | 55.5 | 30.3 | 0.1 | 14.1 | 1008 | -5.43 | 1 | 0 | partially open | vacuum increased
BHGV0040 | 2021-03-23 10:19 | 55.3 | 30.4 | 0 | 14.3 | 1008 | -9.14 | 1 | 0 | partially open | no vacuum change
BHLC001B | 2021-03-23 10:21 | 1 | 4 | 13.8 | 81.2 | 1008 | 0.39 | 1 | 0 | closed | no vacuum change
BHGV0009 | 2021-03-23 10:23 | 56.7 | 29.7 | 0.3 | 13.3 | 1008 | -7.65 | 1 | 0 | partially open | vacuum increased
BHGV0009 | 2021-03-23 10:23 | 58.2 | 30.6 | 0.2 | 11 | 1008 | -10.85 | 1 | 0 | partially open | no vacuum change
BHLC0003 | 2021-03-23 10:26 | 10.1 | 7.9 | 14.6 | 67.4 | 1008 | -0.14 | 0 | 0 | closed | no vacuum change
BHGV0301 | 2021-03-23 10:32 | 61.1 | 37.4 | 0.5 | 1 | 1007 | -0.63 | 2 | 0 | fully open | no vacuum change
BHGV0012 | 2021-03-23 10:37 | 50.9 | 37.3 | 0.1 | 11.7 | 1006 | -9.87 | 2 | 0 | fully open | no vacuum change
BHR00003 | 2021-03-23 10:39 | 63.1 | 31.1 | 1.4 | 4.4 | 1006 | 5.37 | 2 | 0 | closed | vacuum increased
BHR00003 | 2021-03-23 10:40 | 62.4 | 30.9 | 1.5 | 5.2 | 1006 | -8.78 | 1 | 0 | partially open | no vacuum change
BHGV0046 | 2021-03-23 10:41 | 61.9 | 41 | 0.2 | 0 | 1006 | -0.55 | 3 | 0 | closed | vacuum increased
BHGV0046 | 2021-03-23 10:41 | 61.2 | 41.2 | 0 | 0 | 1006 | -1.04 | 3 | 0 | partially open | no vacuum change
BHGV0041 | 2021-03-23 10:42 | 50.2 | 33.7 | 0.4 | 15.7 | 1006 | -9.7 | 2 | 0 | fully open | no vacuum change
BHGV0042 | 2021-03-23 10:47 | 36.3 | 11.2 | 14.4 | 38.1 | 1007 | 0.27 | 1 | 0 | closed | no vacuum change
BHGV0043 | 2021-03-23 10:50 | 68 | 35.2 | 0 | 0 | 1007 | 1.54 | 2 | 0 | fully open | no vacuum change
BHGV0007 | 2021-03-23 10:53 | 72.9 | 29.8 | 0 | 0 | 1007 | 0.61 | 1 | 0 | partially open | no vacuum change
BHGV0008 | 2021-03-23 10:57 | 22.8 | 13.5 | 10.8 | 52.9 | 1007 | 9.07 | 10 | 0 | closed | no vacuum change
BHLC002R | 2021-03-23 10:59 | 67.8 | 34.9 | 0.1 | 0 | 1007 | 0.96 | 2 | 0 | fully open | no vacuum change
BHGV0044 | 2021-03-23 11:01 | 67.2 | 35.6 | 0 | 0 | 1007 | 1.46 | 2 | 0 | partially open | no vacuum change
BHR00001 | 2021-03-23 11:03 | 68.9 | 34.5 | 0 | 0 | 1006 | 1.08 | 1 | 0 | fully open | no vacuum change
BHGV0001 | 2021-03-23 11:04 | 65.7 | 36.8 | 0 | 0 | 1006 | 2.35 | 1 | 0 | fully open | no vacuum change
BHGV0006 | 2021-03-23 11:06 | 63 | 36.7 | 0.5 | 0 | 1007 | 1.9 | 0 | 0 | partially open | no vacuum change
BHGV0003 | 2021-03-23 11:07 | 69.8 | 34.3 | 0 | 0 | 1007 | 0.44 | 2 | 0 | fully open | no vacuum change
BHR0001B | 2021-03-23 11:08 | 67.2 | 35.2 | 0 | 0 | 1007 | 1.39 | 1 | 0 | fully open | no vacuum change
BHGV0004 | 2021-03-23 11:09 | 56.7 | 28.7 | 0.3 | 14.3 | 1007 | 1.35 | 2 | 0 | partially open | no vacuum change
BHLC002B | 2021-03-23 11:11 | 53 | 31.6 | 2.2 | 13.2 | 1007 | -0.6 | 3 | 0 | partially open | no vacuum change
BHGV0045 | 2021-03-23 11:15 | 64.8 | 37.2 | 0.9 | 0 | 1005 | 1.57 | 1 | 0 | partially open | no vacuum change
BHLC002B | 2021-03-23 11:17 | 62.7 | 37.9 | 0.2 | 0 | 1005 | 1.75 | 4 | 0 | closed | vacuum increased
BHLC002B | 2021-03-23 11:17 | 62.7 | 38.3 | 0.1 | 0 | 1005 | 1.58 | 4 | 0 | partially open | no vacuum change
BHGV0026 | 2021-03-23 11:22 | 63 | 38.5 | 0.1 | 0 | 1005 | 1.97 | 3 | 0 | fully open | no vacuum change
BHR0002B | 2021-03-23 11:27 | 41 | 24.3 | 5 | 29.7 | 1005 | -0.08 | 3 | 0 | closed | no vacuum change
BHGV000A | 2021-03-23 11:29 | 60.7 | 41.8 | 0 | 0 | 1005 | 0.49 | 3 | 0 | fully open | no vacuum change
BHGV0027 | 2021-03-23 11:32 | 59.9 | 41 | 0.4 | 0 | 1005 | 0.97 | 1 | 0 | fully open | no vacuum change
BHGV0047 | 2021-03-23 11:33 | 62.4 | 38.7 | 0.3 | 0 | 1006 | 0.44 | 2 | 0 | partially open | no vacuum change
BHM050MB | 2021-03-23 11:35 | 62.6 | 34.9 | 0.2 | 2.3 | 1006 | 0.91 | 0 | 0 | fully open | no vacuum change
BHGV0025 | 2021-03-23 11:35 | 57.3 | 35.9 | 0 | 6.8 | 1006 | 0.88 | 1 | 0 | partially open | no vacuum change
BHGV0024 | 2021-03-23 11:36 | 63.5 | 36.8 | 0.1 | 0 | 1006 | -0.22 | 1 | 0 | fully open | no vacuum change
BHGV0023 | 2021-03-23 11:37 | 63.5 | 38.8 | 0 | 0 | 1006 | 0.78 | 1 | 0 | closed | no vacuum change
BHGV0022 | 2021-03-23 11:40 | 20.3 | 13.8 | 11.7 | 54.2 | 1006 | 0.45 | 25 | 0 | closed
BHM050MA | 2021-03-23 11:42 | 63.4 | 37 | 0.3 | 0 | 1006 | 0.9 | 4 | 0 | fully open | no vacuum change
BHGV0048 | 2021-03-23 11:43 | 60.7 | 37.8 | 0.3 | 1.2 | 1006 | 0.84 | 1 | 0 | fully open | no vacuum change
BHLC0006 | 2021-03-23 11:46 | 56.8 | 36.4 | 1.2 | 5.6 | 1006 | -0.04 | 1 | 0 | closed | vacuum increased
BHLC0006 | 2021-03-23 11:47 | 58.1 | 36.8 | 1 | 4.1 | 1006 | -0.99 | 2 | 0 | partially open | no vacuum change
BHLC006B | 2021-03-23 11:48 | 57.7 | 36.7 | 0.7 | 4.9 | 1005 | -8.04 | 1 | 0 | fully open | no vacuum change
BHLC0005 | 2021-03-23 11:49 | 35.6 | 41.4 | 1.6 | 21.4 | 1005 | 0.97 | 3 | 0 | closed | no vacuum change
BHGV0029 | 2021-03-23 11:50 | 63.1 | 38.5 | 0.4 | 0 | 1005 | 1.1 | 1 | 0 | fully open | no vacuum change
BHGV000C | 2021-03-23 11:51 | 59.7 | 38.4 | 0.3 | 1.6 | 1005 | -0.02 | 0 | 0 | fully open | no vacuum change
BHGV0028 | 2021-03-23 11:52 | 60 | 36.9 | 0.6 | 2.5 | 1005 | 0.45 | 1 | 0 | closed | vacuum increased
BHGV0028 | 2021-03-23 11:53 | 61.2 | 38.6 | 0.1 | 0.1 | 1005 | 1 | 2 | 0 | fully open | no vacuum change
BHGV000B | 2021-03-23 11:55 | 60.6 | 38 | 0.3 | 1.1 | 1005 | 0.67 | 1 | 0 | fully open | no vacuum change
BHGV0030 | 2021-03-23 11:57 | 50.8 | 36.1 | 0 | 13.1 | 1005 | -6.59 | 2 | 0 | fully open | no vacuum change
BHR00005 | 2021-03-23 11:59 | 0.1 | 2.7 | 17.1 | 80.1 | 1005 | 105.2 | 0 | 0 | closed | no vacuum change
BHGV0031 | 2021-03-23 12:01 | 33.6 | 32.6 | 0.9 | 32.9 | 1005 | -2.52 | 1 | 0 | closed | no vacuum change
BHGV0032 | 2021-03-23 12:03 | 60.3 | 41.8 | 0.3 | 0 | 1006 | 0.72 | 1 | 0 | fully open | no vacuum change
BHGV0033 | 2021-03-23 12:04 | 60.1 | 41.1 | 0.3 | 0 | 1005 | 0.4 | 2 | 0 | closed | vacuum increased
BHGV0033 | 2021-03-23 12:05 | 60.2 | 41.2 | 0.1 | 0 | 1005 | -3.16 | 3 | 0 | partially open | no vacuum change
BHR0006B | 2021-03-23 12:06 | 63.1 | 39.8 | 0 | 0 | 1005 | 9.18 | 2 | 0 | closed | vacuum increased
BHR0006B | 2021-03-23 12:06 | 63.4 | 39.9 | 0 | 0 | 1005 | -1.19 | 3 | 0 | partially open | no vacuum change
BHGV0049 | 2021-03-23 12:07 | 62.2 | 40 | 0 | 0 | 1006 | -2.14 | 2 | 0 | partially open | vacuum increased
BHGV0049 | 2021-03-23 12:07 | 62.1 | 40.3 | 0 | 0 | 1006 | -3.71 | 1 | 0 | partially open | no vacuum change
BHPW0006 | 2021-03-23 12:09 | 5.8 | 17.4 | 5.4 | 71.4 | 1006 | 1.9 | 0 | 0 | closed | no vacuum change
BHPW0005 | 2021-03-23 12:11 | 58.5 | 36.7 | 1 | 3.8 | 1006 | -7.07 | 0 | 0 | closed | vacuum increased
BHPW0005 | 2021-03-23 12:12 | 58.5 | 36.8 | 1 | 3.7 | 1006 | -7.01 | 0 | 0 | partially open | no vacuum change
BHPW0004 | 2021-03-23 12:13 | 53.3 | 29.9 | 0 | 16.8 | 1006 | -1.11 | 0 | 0 | closed | vacuum increased
BHPW0004 | 2021-03-23 12:13 | 53.6 | 30.5 | 0 | 15.9 | 1006 | -3.12 | 0 | 0 | partially open | no vacuum change
BHPW0003 | 2021-03-23 12:15 | 26.6 | 19.9 | 2.5 | 51 | 1006 | -5.32 | 0 | 0 | closed | no vacuum change
BHPW0002 | 2021-03-23 12:16 | 26.7 | 19.3 | 2.6 | 51.4 | 1006 | 0.89 | 0 | 0 | closed | no vacuum change
BHPW0001 | 2021-03-23 12:18 | 14.7 | 7.1 | 14.7 | 63.5 | 1006 | -6.97 | 0 | 0 | closed | no vacuum change
BHGW0034 | 2021-03-23 12:19 | 40.3 | 17.4 | 0.2 | 42.1 | 1006 | 0.2 | 0 | 0 | closed | vacuum increased
BHGW0034 | 2021-03-23 12:19 | 40.5 | 17.7 | 0.1 | 41.7 | 1006 | -1.24 | 0 | 0 | partially open | no vacuum change
BHG010MA | 2021-03-23 12:21 | 51 | 30.6 | 1.6 | 16.8 | 1006 | -9.45 | 0 | 0 | fully open | no vacuum change
BHG01MDA | 2021-03-23 12:25 | 54 | 34.6 | 0.4 | 11 | 1006 | 201.36 | 1 | 0 | fully open | no vacuum change
BHG01MDA | 2021-03-23 12:35 | 53.3 | 35.1 | 0.4 | 11.2 | 1006 | 154.97 | 2 | 0 | fully open | no vacuum change

## April 2021
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-04-01
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 1013 | 0.06 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 0.2 | 17.9 | 81.9 | 0 | 0 | 1014 | 0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 18 | 81.8 | 0 | 0 | 1015 | 0.06 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 1013 | 0.08 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 17.3 | 7 | 12.3 | 63.4 | 0 | 0 | 1013 | -0.06 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.8 | 7.6 | 14.3 | 65.3 | 0 | 0 | 1013 | 0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1013 | 0.06 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 3.5 | 8.6 | 87.9 | 0 | 0 | 1013 | 0.1 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.7 | 17.6 | 81.7 | 0 | 0 | 1013 | 0.38 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.8 | 82.1 | 0 | 0 | 1012 | 0.1 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.2 | 16.7 | 82.1 | 0 | 0 | 1012 | 0.16 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.3 | 17.5 | 82.1 | 0 | 0 | 1012 | 0.16 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.2 | 4.9 | 10.9 | 84 | 0 | 0 | 1012 | -0.02 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.4 | 17.5 | 82.1 | 0 | 0 | 1012 | 0.36 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2 | 16.8 | 81.2 | 0 | 0 | 1013 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1012 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.3 | 16.2 | 81.5 | 0 | 0 | 1013 | 0.01 | 1 | 9.9 | 0.5 | 4.95
Date | 2021-04-08
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1006 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.3 | 16.5 | 81.2 | 0 | 0 | 1007 | 0.01 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1008 | 0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1007 | 0.04 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 18.9 | 7.3 | 12.4 | 61.4 | 0 | 0 | 1007 | 0.11 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 9.8 | 5.8 | 14.8 | 69.6 | 0 | 0 | 1006 | 0.02 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.6 | 82.3 | 0 | 0 | 1006 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 0.7 | 14.8 | 84.5 | 0 | 0 | 1007 | -0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.2 | 17.7 | 82.1 | 0 | 0 | 1007 | 0.22 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1007 | 0.02 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 17.3 | 82.2 | 0 | 0 | 1007 | 0.02 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 0.6 | 14.3 | 84.9 | 0 | 0 | 1007 | 0.05 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 3 | 12.9 | 84.1 | 0 | 0 | 1006 | 0.11 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.3 | 17.6 | 82.1 | 0 | 0 | 1006 | -0.02 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.6 | 16.1 | 80.3 | 0 | 0 | 1005 | 0.01 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 17.7 | 82.2 | 0 | 0 | 1005 | 0 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 16.3 | 81.6 | 0 | 0 | 1005 | 0.03 | 1 | 9.9 | 0.5 | 4.95
Date | 2021-04-13
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 19.1 | 80.8 | 0 | 0 | 1018 | 0.1 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.3 | 18.5 | 79.2 | 0 | 0 | 1019 | 0.09 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0.1 | 0.1 | 19.9 | 79.9 | 0 | 0 | 1019 | 0.07 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 13.5 | 6.6 | 13 | 66.9 | 0 | 0 | 1018 | 0.14 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.6 | 7.3 | 15.8 | 64.3 | 0 | 0 | 1018 | 0.08 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1006 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.5 | 10.6 | 86.8 | 0 | 0 | 1019 | -0.63 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0.1 | 0.4 | 19.7 | 79.8 | 0 | 0 | 1019 | -0.75 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.1 | 19.8 | 80 | 0 | 0 | 1018 | 0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 0.4 | 19.4 | 80.1 | 0 | 0 | 1018 | 0.06 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.4 | 1.7 | 16.5 | 81.4 | 0 | 0 | 1016 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 0.1 | 19.6 | 80.2 | 0 | 0 | 1018 | 0.04 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.3 | 19.3 | 80.3 | 0 | 0 | 1018 | 0.01 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.6 | 17.3 | 79.1 | 0 | 0 | 1017 | 0.08 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 20 | 79.9 | 0 | 0 | 1017 | 0.07 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 2.1 | 16.3 | 81.6 | 0 | 0 | 1017 | 0.07 | 1 | 9.9 | 0.5 | 4.95
Brookhill Landfill |  |  | Borehole Gas Monitoring
Date | 2021-04-23
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.4 | 18.8 | 80.8 | 0 | 0 | 1011 | 0.04 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 1.6 | 18.6 | 79.8 | 0 | 0 | 1012 | 0.35 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0 | 0.2 | 19.4 | 80.4 | 0 | 0 | 1013 | 0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | 0 | 0.1 | 16.8 | 83.1 | 0 | 0 | 1012 | 0.06 | 1 | 10 | 0.5 | 5
BK BH 8 |  | 11.9 | 5.8 | 14.7 | 67.6 | 0 | 0 | 1012 | 0.08 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 12.6 | 7.3 | 15.5 | 64.6 | 1 | 0 | 1011 | 0.07 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1006 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 3 | 6.8 | 90.2 | 0 | 0 | 1012 | -0.22 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 0.8 | 18.8 | 80.4 | 0 | 0 | 1012 | 0.19 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 19.3 | 80.7 | 0 | 0 | 1011 | 0.07 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.6 | 18.7 | 80.7 | 0 | 0 | 1011 | 0.27 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 5 | 9.5 | 85.3 | 1 | 0 | 1011 | 0.15 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 0 | 19.3 | 80.7 | 0 | 0 | 1011 | 0.09 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | 0.1 | 1.2 | 12.9 | 85.8 | 0 | 0 | 1011 | 0.1 | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 0.1 | 19.1 | 80.7 | 0 | 0 | 1011 | 0.38 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 3.4 | 16.8 | 79.8 | 0 | 0 | 1011 | 0.04 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 19.4 | 80.6 | 0 | 0 | 1011 | 0.01 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.2 | 18.4 | 80.4 | 0 | 0 | 1011 | 0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2021-04-29
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 9 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 1.5 | 19.5 | 79 | 0 | 0 | 999 | -0.08 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.9 | 18.1 | 79 | 0 | 0 | 1000 | 0.15 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.1 | 1 | 19.3 | 79.6 | 0 | 0 | 1000 | -0.05 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 18.2 | 6.4 | 14.2 | 61.2 | 0 | 0 | 999 | -0.03 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 10.8 | 7.3 | 16.4 | 65.5 | 0 | 0 | 999 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.2 | 17.6 | 82.2 | 0 | 0 | 1006 | 0.05 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.2 | 6.8 | 91 | 0 | 0 | 1000 | -0.46 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 1 | 18.2 | 80.8 | 0 | 0 | 999 | -0.45 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.5 | 19.5 | 80 | 0 | 0 | 999 | 0.1 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 1.2 | 19 | 79.8 | 0 | 0 | 999 | -0.04 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.2 | 5.5 | 6.4 | 87.9 | 0 | 0 | 999 | -0.02 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.3 | 16.5 | 81.2 | 1 | 0 | 999 | -0.07 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 1.5 | 18.3 | 80.2 | 0 | 0 | 999 | 0.23 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 1.9 | 17.5 | 80.6 | 0 | 0 | 998 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.6 | 19.9 | 79.5 | 0 | 0 | 998 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.4 | 18.7 | 79.9 | 0 | 0 | 998 | -0.01 | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA13202 | MCERTS certified instrument
Date downloaded | 2021-04-23 12:58 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2021-04-12
Date of last factory calibration | 2021-02-24
Next service due | 2021-08-24
Date of last Gas Check | N/A
Security code | [00AEB064]
ID | DATE | CH4 | CO2 | O2 | BALANCE | PEAKCH4 | PEAKCO2 | MIN O2 | BARO | REL.PRESSURE | CO | H2S | SITECHOSEN 1 | SITECHOSEN 2
|  | % | % | % | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2021-04-23 10:02 | 50.7 | 32.3 | 1.8 | 15.2 | 52.3 | 32.3 | 1.8 | 1015 | 156.13 | 3 | 0
BHG010MB | 2021-04-23 10:07 | 49 | 31.8 | 2.2 | 17 | 49.1 | 31.9 | 2.2 | 1014 | -5.54 | 3 | 0
BHG01MDB | 2021-04-23 10:11 | 50.5 | 31.8 | 1.8 | 15.9 | 50.5 | 31.7 | 1.9 | 1014 | 206.28 | 4 | 0
BHGV0035 | 2021-04-23 10:13 | 64 | 35.7 | 0.3 | 0 | 64.1 | 35.7 | 0.3 | 1013 | -0.12 | 3 | 0 | sunny | light wind
BHGV0035 | 2021-04-23 10:14 | 64 | 37 | 0.2 | 0 |  |  |  | 1013 | -0.61 | 3 | 0 | sunny | light wind
BHGV0036 | 2021-04-23 10:15 | 66.5 | 33.6 | 0.2 | 0 | 66.3 | 36.6 | 0.2 | 1014 | -0.13 | 3 | 0 | sunny | light wind
BHGV0036 | 2021-04-23 10:16 | 67.4 | 33.1 | 0.3 | 0 |  |  |  | 1014 | -0.88 | 4 | 0 | sunny | light wind
BHGV0037 | 2021-04-23 10:18 | 56.3 | 28.7 | 0.1 | 14.9 | 67.4 | 33.3 | 0.1 | 1014 | -0.17 | 3 | 0 | sunny | light wind
BHGV0037 | 2021-04-23 10:19 | 56.3 | 28.4 | 0.2 | 15.1 |  |  |  | 1014 | -1.29 | 2 | 0 | sunny | light wind
BHM010MB | 2021-04-23 10:20 | 60.4 | 39.3 | 0.2 | 0.1 | 60.6 | 39.1 | 0.2 | 1014 | -4.07 | 3 | 0 | sunny | light wind
BHGV0018 | 2021-04-23 10:22 | 59.3 | 40.8 | 0 | 0 | 59.8 | 40.7 | 0 | 1014 | -4.09 | 5 | 0 | sunny | light wind
BHLC004B | 2021-04-23 10:23 | 60.4 | 41.2 | 0.1 | 0 | 60.4 | 41.2 | 0 | 1014 | 1.56 | 4 | 0 | sunny | light wind
BHLC004B | 2021-04-23 10:26 | 56.7 | 39.5 | 1 | 2.8 | 60.4 | 41.3 | 0.1 | 1014 | -1.49 | 4 | 0 | sunny | light wind
BHR0004B | 2021-04-23 10:27 | 29.2 | 19.1 | 0.5 | 51.2 | 57 | 39.6 | 0.5 | 1013 | 4.9 | 3 | 0 | sunny | light wind
BHGV0015 | 2021-04-23 10:28 | 63.3 | 37.2 | 0.3 | 0 | 63.3 | 37.2 | 0.3 | 1013 | -3.81 | 3 | 0 | sunny | light wind
BHGV0014 | 2021-04-23 10:30 | 50.1 | 36.3 | 0.3 | 13.3 | 62.3 | 39.8 | 0.1 | 1013 | 0.79 | 3 | 0 | sunny | light wind
BHGV0014 | 2021-04-23 10:31 | 53.6 | 38.2 | 0.1 | 8.1 | 53.6 | 38.2 | 0.1 | 1013 | -1.67 | 3 | 0 | sunny | light wind
BHGV0013 | 2021-04-23 10:33 | 3.4 | 4.4 | 17.8 | 74.4 | 53.9 | 38.2 | 0.1 | 1013 | -3.85 | 1 | 0 | sunny | light wind
BHGV0016 | 2021-04-23 10:34 | 0.1 | 1.4 | 19.5 | 79 | 3.5 | 4.5 | 17.3 | 1014 | -0.71 | 1 | 0 | sunny | light wind
BHM010MA | 2021-04-23 10:37 | 56.3 | 39.2 | 0.7 | 3.8 | 56.3 | 39.2 | 0.7 | 1014 | -3.87 | 4 | 0 | sunny | light wind
BHGV0038 | 2021-04-23 10:40 | 60.5 | 37.8 | 0.3 | 1.4 | 60.7 | 37.8 | 0.3 | 1013 | 0.17 | 3 | 0 | sunny | light wind
BHGV0038 | 2021-04-23 10:41 | 60.3 | 37.3 | 0.4 | 2 |  |  |  | 1013 | -0.34 | 3 | 0 | sunny | light wind
BHGV0039 | 2021-04-23 10:42 | 62.8 | 31.7 | 1.2 | 4.3 | 62.9 | 37.9 | 0.6 | 1014 | -0.71 | 3 | 0 | sunny | light wind
BHGV0039 | 2021-04-23 10:42 | 63.1 | 31.7 | 1.1 | 4.1 |  |  |  | 1014 | -2.23 | 3 | 0 | sunny | light wind
BHGV0011 | 2021-04-23 10:44 | 69 | 31.5 | 0.8 | 0 | 69 | 31.7 | 0.8 | 1014 | 0.46 | 3 | 0 | sunny | light wind
BHGV0010 | 2021-04-23 10:46 | 71.5 | 30.7 | 0.1 | 0 | 71.5 | 32.2 | 0.1 | 1014 | 14.29 | 3 | 0 | sunny | light wind
BHGV0010 | 2021-04-23 10:47 | 71.5 | 30.5 | 0.1 | 0 | 71.5 | 30.5 | 0.1 | 1014 | -3.85 | 3 | 0 | sunny | light wind
BHGV0040 | 2021-04-23 10:50 | 62.9 | 31.6 | 0.1 | 5.4 | 71.6 | 31.6 | 0.1 | 1013 | -3.57 | 2 | 0 | sunny | light wind
BHGV0040 | 2021-04-23 10:51 | 63 | 32 | 0.1 | 4.9 |  |  |  | 1013 | -3.66 | 2 | 0 | sunny | light wind
BHLC001B | 2021-04-23 10:52 | 1 | 2.6 | 15.5 | 80.9 | 62.8 | 32 | 0.1 | 1013 | 0.13 | 3 | 0 | sunny | light wind
BHGV0009 | 2021-04-23 10:53 | 58.7 | 34.5 | 0.5 | 6.3 | 59.2 | 34.5 | 0.6 | 1013 | -3.92 | 2 | 0 | sunny | light wind
BHGV0009 | 2021-04-23 10:53 | 58.6 | 35.2 | 0.2 | 6 |  |  |  | 1013 | -3.96 | 3 | 0 | sunny | light wind
BHLC0003 | 2021-04-23 10:54 | 20.6 | 14.1 | 12.2 | 53.1 | 57.4 | 35.7 | 0.4 | 1013 | 0.47 | 3 | 0 | sunny | light wind
BHGV0301 | 2021-04-23 10:56 | 65.3 | 37.1 | 0.3 | 0 | 65.8 | 37.1 | 0.3 | 1013 | -0.33 | 3 | 0 | sunny | light wind
BHGV0012 | 2021-04-23 10:58 | 58.5 | 39.8 | 0.1 | 1.6 | 64.4 | 39.8 | 0.1 | 1013 | -2.11 | 4 | 0 | sunny | light wind
BHR00003 | 2021-04-23 11:00 | 45.8 | 27.4 | 2.5 | 24.3 | 58.2 | 40.1 | 0.2 | 1012 | 15.9 | 2 | 0 | sunny | light wind
BHR00003 | 2021-04-23 11:01 | 45.6 | 27.2 | 2.7 | 24.5 | 45.8 | 27.3 | 2.5 | 1012 | -1.95 | 2 | 0 | sunny | light wind
BHGV0046 | 2021-04-23 11:03 | 55.6 | 38.3 | 0 | 6.1 | 56.8 | 38.3 | 0 | 1012 | -3.09 | 4 | 0 | sunny | light wind
BHGV0046 | 2021-04-23 11:03 | 55.4 | 38.2 | 0.1 | 6.3 |  |  |  | 1012 | -4.24 | 3 | 0 | sunny | light wind
BHGV0041 | 2021-04-23 11:04 | 59.4 | 36.1 | 0.1 | 4.4 | 59.4 | 38.1 | 0.1 | 1011 | -3.39 | 1 | 0 | sunny | light wind
BHGV0042 | 2021-04-23 11:06 | 34.2 | 17.2 | 6.6 | 42 | 59.6 | 35.4 | 0.1 | 1013 | 0.21 | 2 | 0 | sunny | light wind
BHGV0043 | 2021-04-23 11:08 | 49.6 | 30.2 | 0.3 | 19.9 | 49.8 | 30.2 | 0.3 | 1013 | -3.58 | 2 | 0 | sunny | light wind
BHGV0007 | 2021-04-23 11:09 | 56.3 | 24.4 | 3.5 | 15.8 | 56.3 | 30.3 | 0.4 | 1013 | -3.68 | 2 | 0 | sunny | light wind
BHGV0008 | 2021-04-23 11:13 | 22.3 | 16.1 | 8.5 | 53.1 | 56.3 | 24.4 | 3.4 | 1013 | 2.39 | 8 | 0 | sunny | light wind
BHLC002R | 2021-04-23 11:18 | 64.1 | 30.7 | 0.6 | 4.6 | 64.1 | 30.5 | 0.6 | 1013 | -3.58 | 4 | 0 | sunny | light wind
BHGV0044 | 2021-04-23 11:19 | 28 | 24.2 | 2.9 | 44.9 | 63.5 | 32.1 | 0.3 | 1013 | -3.75 | 2 | 0 | sunny | light wind
BHGV0044 | 2021-04-23 11:19 | 27.3 | 23.7 | 3 | 46 |  |  |  | 1013 | 0.1 | 2 | 0 | sunny | light wind
BHR00001 | 2021-04-23 11:22 | 63 | 33.4 | 1.2 | 2.4 | 63.2 | 33.4 | 1.2 | 1012 | -2.06 | 2 | 0 | sunny | light wind
BHGV0001 | 2021-04-23 11:23 | 62.8 | 31 | 1 | 5.2 | 62.9 | 33.8 | 1 | 1012 | -3.93 | 2 | 0 | sunny | light wind
BHGV0045 | 2021-04-23 11:25 | 59.6 | 32 | 0.1 | 8.3 | 63 | 32 | 0.1 | 1011 | -3.75 | 2 | 0 | sunny | light wind
BHGV0045 | 2021-04-23 11:25 | 59.6 | 32.3 | 0 | 8.1 |  |  |  | 1011 | -3.64 | 2 | 0 | sunny | light wind
BHGV0006 | 2021-04-23 11:27 | 60.4 | 32.2 | 1 | 6.4 | 60.3 | 32.9 | 0.2 | 1012 | -2.45 | 2 | 0 | sunny | light wind
BHGV0006 | 2021-04-23 11:27 | 60 | 32.2 | 0.9 | 6.9 |  |  |  | 1012 | -3.74 | 3 | 0 | sunny | light wind
BHGV0003 | 2021-04-23 11:28 | 70.9 | 32.2 | 0.4 | 0 | 70.7 | 32.6 | 0.4 | 1012 | -3.83 | 3 | 0 | sunny | light wind
BHR0001B | 2021-04-23 11:29 | 63.4 | 33.9 | 0.7 | 2 | 70.8 | 33.8 | 0 | 1012 | -3.93 | 3 | 0 | sunny | light wind
BHGV0004 | 2021-04-23 11:30 | 27.1 | 27.9 | 0.5 | 44.5 | 63.3 | 34.6 | 0.6 | 1012 | -3.65 | 3 | 0 | sunny | light wind
BHGV0004 | 2021-04-23 11:30 | 27.3 | 26.7 | 0.1 | 45.9 |  |  |  | 1012 | 0.11 | 2 | 0 | sunny | light wind
BHLC002B | 2021-04-23 11:32 | 32 | 20.1 | 7.7 | 40.2 | 32.2 | 26.9 | 0.1 | 1012 | -0.57 | 8 | 0 | sunny | light wind
BHGV0021 | 2021-04-23 11:34 | 67.2 | 36 | 0.2 | 0 | 67.4 | 35.8 | 0.2 | 1013 | -3.41 | 4 | 0 | sunny | light wind
BHGV0202 | 2021-04-23 11:38 | 62.1 | 36.1 | 0.6 | 1.2 | 64.5 | 36.1 | 0.5 | 1011 | -1.5 | 2 | 0 | sunny | light wind
BHGV0026 | 2021-04-23 11:41 | 62.1 | 37.4 | 0.4 | 0.1 | 64.1 | 37.4 | 0.2 | 1011 | -1.32 | 3 | 0 | sunny | light wind
BHGV0047 | 2021-04-23 11:42 | 55.2 | 35.5 | 0.3 | 9 | 62.9 | 39 | 0.1 | 1011 | -3.54 | 4 | 0 | sunny | light wind
BHM050MB | 2021-04-23 11:44 | 56.8 | 36.5 | 0.1 | 6.6 | 56.8 | 36.5 | 0.1 | 1012 | -3.53 | 4 | 0 | sunny | light wind
BHGV0025 | 2021-04-23 11:45 | 41.7 | 32.5 | 0 | 25.8 | 56.7 | 36.8 | 0 | 1012 | -3.67 | 4 | 0 | sunny | light wind
BHGV0024 | 2021-04-23 11:46 | 63.5 | 35.4 | 0 | 1.1 | 63.6 | 35.2 | 0 | 1012 | -3.6 | 4 | 0 | sunny | light wind
BHGV0023 | 2021-04-23 11:47 | [7 empty] | 1012 | 0 | 2 | 0 | sunny | light wind
BHGV0022 | 2021-04-23 11:58 | 5.3 | 1.2 | 18.5 | 75 | 5.3 | 1.6 | 17.3 | 1012 | 0.11 | 45 | 0 | sunny | light wind
BHGV0048 | 2021-04-23 11:59 | 59.2 | 33.4 | 0.2 | 7.2 | 69.4 | 33.4 | 0.2 | 1012 | -3.6 | 4 | 0 | sunny | light wind
BHM050MA | 2021-04-23 12:00 | 59.2 | 36.6 | 0.2 | 4 | 59.3 | 36.5 | 0.2 | 1012 | -3.78 | 2 | 0 | sunny | light wind
BHLC0006 | 2021-04-23 12:02 | 3.3 | 4.6 | 17.7 | 74.4 | 60.3 | 37.1 | 0.3 | 1011 | -0.27 | 1 | 0 | sunny | light wind
BHLC0006 | 2021-04-23 12:03 | 3.4 | 4.3 | 17.9 | 74.4 |  |  |  | 1011 | 0.09 | 0 | 0 | sunny | light wind
BHLC006B | 2021-04-23 12:04 | 60.7 | 39.6 | 0.2 | 0 | 71.3 | 39 | 0.1 | 1010 | -2.95 | 2 | 0 | sunny | light wind
BHLC0005 | 2021-04-23 12:06 | 60 | 41.2 | 0.1 | 0 | 60.2 | 41.2 | 0.1 | 1010 | 0.5 | 2 | 0 | sunny | light wind
BHLC0005 | 2021-04-23 12:06 | 59.5 | 41.5 | 0.3 | 0 |  |  |  | 1010 | -0.7 | 3 | 0 | sunny | light wind
BHR00005 | 2021-04-23 12:11 | 0.2 | 4.8 | 18.5 | 76.5 | 58.7 | 41 | 0.4 | 1010 | 91.93 | 1 | 0 | sunny | light wind
BHGV0029 | 2021-04-23 12:14 | 67.3 | 33.3 | 0.4 | 0 | 67.4 | 33.3 | 0.4 | 1010 | -3.36 | 2 | 0 | sunny | light wind
BHGV000C | 2021-04-23 12:16 | 60.3 | 40.9 | 0 | 0 | 63.9 | 40.8 | 0 | 1010 | -1.63 | 2 | 0 | sunny | light wind
BHGV0028 | 2021-04-23 12:17 | 60.3 | 40.1 | 0.1 | 0 | 60.3 | 41.5 | 0.1 | 1010 | -3.4 | 3 | 0 | sunny | light wind
BHGV000B | 2021-04-23 12:22 | 60.3 | 38.8 | 0.1 | 0.8 | 60.4 | 38.8 | 0.1 | 1010 | -1.94 | 1 | 0 | sunny | light wind
BHGV0027 | 2021-04-23 12:23 | 53.7 | 37.3 | 1.1 | 7.9 |  |  |  | 1010 | 0.05 | 1 | 0 | sunny | light wind
BHGV0030 | 2021-04-23 12:26 | 55.6 | 36.1 | 0.8 | 7.5 | 55.6 | 37 | 0.3 | 1010 | -2.52 | 2 | 0 | sunny | light wind
BHGV0031 | 2021-04-23 12:27 | 59.8 | 39.4 | 0.2 | 0.6 | 60.3 | 39.3 | 0.1 | 1010 | -0.68 | 2 | 0 | sunny | light wind
BHGV0031 | 2021-04-23 12:27 | 59.9 | 39.7 | 0.2 | 0.2 |  |  |  | 1010 | -2.79 | 2 | 0 | sunny | light wind
BHGV0033 | 2021-04-23 12:30 | 47.2 | 36 | 1.3 | 15.5 | 60.5 | 39.5 | 0.2 | 1010 | -1.94 | 2 | 0 | sunny | light wind
BHGV0032 | 2021-04-23 12:31 | 61.2 | 35.2 | 0.3 | 3.3 | 61.3 | 34.7 | 0.3 | 1010 | 0.24 | 1 | 0 | sunny | light wind
BHR0006B | 2021-04-23 12:33 | 63.7 | 38.5 | 0 | 0 | 63.7 | 41 | 0 | 1010 | 10.36 | 2 | 0 | sunny | light wind
BHR0006B | 2021-04-23 12:34 | 63.8 | 38.2 | 0 | 0 | 63.7 | 38.2 | 0 | 1010 | 3.62 | 2 | 0 | sunny | light wind
BHGV0049 | 2021-04-23 12:35 | 34.2 | 31.6 | 0.4 | 33.8 | 63.9 | 38.3 | 0 | 1011 | -1.9 | 0 | 0 | sunny | light wind
BHGV0049 | 2021-04-23 12:35 | 34.5 | 28.7 | 0.4 | 36.4 |  |  |  | 1011 | 0 | 0 | 0 | sunny | light wind
BHPW0006 | 2021-04-23 12:37 | 22.5 | 23.6 | 2.6 | 51.3 | 35 | 27.8 | 0.4 | 1011 | -0.85 | 0 | 0 | sunny | light wind
BHPW0005 | 2021-04-23 12:38 | 46.2 | 24.6 | 1.3 | 27.9 | 46.1 | 24.5 | 1.3 | 1011 | -2.89 | 0 | 0 | sunny | light wind
BHPW0004 | 2021-04-23 12:41 | 31.5 | 21.8 | 1.1 | 45.6 | 46 | 24.8 | 1.1 | 1011 | -0.45 | 0 | 0 | sunny | light wind
BHPW0003 | 2021-04-23 12:42 | 24.6 | 22 | 1.6 | 51.8 | 31.3 | 22 | 1 | 1011 | -1.11 | 0 | 0 | sunny | light wind
BHPW0002 | 2021-04-23 12:43 | [7 empty] | 1011 | -0.05 | 0 | 0 | sunny | light wind
BHPW0001 | 2021-04-23 12:44 | 24.3 | 21 | 1 | 53.7 |  |  |  | 1011 | 0.08 | 0 | 0 | sunny | light wind
BHGW0034 | 2021-04-23 12:45 | 39.3 | 19.6 | 0 | 41.1 | 39.3 | 21 | 0 | 1011 | 0.17 | 0 | 0 | sunny | light wind
BHGW0034 | 2021-04-23 12:45 | 39.4 | 19.6 | 0 | 41 |  |  |  | 1011 | 0.11 | 0 | 0 | sunny | light wind
BHG010MA | 2021-04-23 12:47 | 55.1 | 33 | 1 | 10.9 | 56.9 | 33 | 0 | 1011 | -4.38 | 2 | 0 | sunny | light wind
BHG01MDA | 2021-04-23 12:49 | 56.9 | 35.1 | 0.3 | 7.7 | 57 | 35 | 0.3 | 1011 | 203.73 | 2 | 0 | sunny | light wind
BHG01MDA | 2021-04-23 12:53 | 56.6 | 35.2 | 0.3 | 7.9 | 56.8 | 35.3 | 0.3 | 1011 | 156.97 | 2 | 0 | sunny | light wind

## May 2021
Date | 2021-05-06
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | JS(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 3.2 | 20.8 | 76 | 0 | 0 | 999 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.9 | 18.7 | 78.4 | 0 | 0 | 999 | 0.12 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.9 | 0.8 | 19.7 | 73.6 | 0 | 0 | 999 | -0.3 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 7.9 | 5.4 | 15.4 | 71.3 | 0 | 0 | 999 | -0.16 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 17 | 9.9 | 14.5 | 58.6 | 0 | 0 | 999 | -0.21 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 999 | 0.04 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.1 | 6.8 | 91.1 | 0 | 0 | 999 | -0.24 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.3 | 5.4 | 91.3 | 0 | 0 | 999 | 6.89 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 2.4 | 20.6 | 77 | 0 | 0 | 999 | -0.39 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 3.7 | 19.3 | 77 | 0 | 0 | 999 | -0.26 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 5.2 | 6.1 | 88.6 | 0 | 0 | 999 | -0.04 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0 | 2.3 | 16.2 | 81.5 | 0 | 0 | 999 | -0.05 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.2 | 8.7 | 18.5 | 72.6 | 0 | 0 | 999 | 1.77 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.4 | 20.9 | 76.7 | 0 | 0 | 999 | -0.35 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 1 | 21 | 77 | 0 | 0 | 999 | -0.26 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.2 | 18.5 | 80.3 | 0 | 0 | 999 | -0.02 | 1 | 9.9 | 0.5 | 4.95
Please Note: Trigger level breaches will be hi-lighted: ( Red CH4 ), ( Blue CO2 ), (Orange 50% Rule).
Date | 2021-05-13
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0.1 | 0.1 | 20 | 79.8 | 0 | 0 | 994 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0.1 | 2.4 | 17.5 | 80 | 0 | 0 | 994 | 0 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.5 | 0 | 19.5 | 80 | 0 | 0 | 994 | -0.3 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 10.8 | 7 | 13.9 | 68.3 | 0 | 0 | 994 | 0.05 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 15.4 | 9 | 14.9 | 60.7 | 0 | 0 | 993 | 0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.3 | 17.4 | 82.3 | 0 | 0 | 994 | 0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0.1 | 2.1 | 11.5 | 86.3 | 0 | 0 | 994 | 0.05 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 2 | 4.3 | 93.7 | 0 | 0 | 994 | 0.04 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0.1 | 0.8 | 19.7 | 79.4 | 0 | 0 | 993 | 0.05 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0.1 | 1.9 | 19 | 79 | 0 | 0 | 993 | -0.24 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.6 | 3.7 | 18 | 77.7 | 0 | 0 | 993 | 0.03 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 2.1 | 18.3 | 79.5 | 0 | 0 | 993 | 0.55 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0.1 | 3.4 | 18.1 | 78.4 | 0 | 0 | 993 | 0.05 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 16.1 | 79.3 | 0 | 0 | 994 | 0.02 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0.1 | 0.1 | 19.9 | 79.9 | 0 | 0 | 993 | 0.04 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0.1 | 0.3 | 19.9 | 79.7 | 0 | 0 | 993 | 0.11 | 1 | 9.9 | 0.5 | 4.95
Date | 2021-05-18
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 7 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.1 | 19.4 | 80.5 | 0 | 0 | 998 | 0.01 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.7 | 17.4 | 79.3 | 0 | 0 | 999 | 0.07 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.4 | 0 | 19.4 | 80.2 | 0 | 0 | 998 | -0.02 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 11.5 | 6.5 | 14.2 | 67.8 | 0 | 0 | 998 | 0.35 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 14.4 | 8.4 | 14.9 | 62.3 | 0 | 0 | 998 | 0.06 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.2 | 17.2 | 82.6 | 0 | 0 | 998 | 0.02 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 5.3 | 1.4 | 93.3 | 0 | 0 | 999 | 2.66 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 5 | 6 | 89 | 0 | 0 | 999 | -0.54 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0.1 | 19.5 | 80.4 | 0 | 0 | 999 | 0.5 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.5 | 18.9 | 80.6 | 0 | 0 | 999 | -0.42 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 11.3 | 2.9 | 15.5 | 70.3 | 0 | 0 | 999 | 0.24 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.9 | 18 | 80 | 0 | 0 | 998 | 0.49 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0.2 | 19.2 | 80.6 | 0 | 0 | 1000 | 0.13 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 4.6 | 15.1 | 80.3 | 0 | 0 | 998 | 0.12 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0.1 | 19.3 | 80.6 | 0 | 0 | 998 | 0.08 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 0.7 | 18.3 | 81 | 0 | 0 | 998 | 0.09 | 1 | 9.9 | 0.5 | 4.95
Date | 2021-05-28
Weather: | dry
Wind conditions: | Calm
Air Temperature: | 6 | OC
Instrument: | GA2000Plus
Serial No: | GA12599
Calibrated To:
Operative | MJ(YLEM)
Monitoring | Time | CH4 | CO2 | O2 | Balance | CO | H2S | Baro | Rel Pressure | Trig Lev | Trig Lev | Trig Lev | Trig Lev
Point | Hrs | % | % | % | % | ppm | ppm | mb | mb | CH4 % | CO2 % | CH4 50% | CO2 50 %
BK BH 1 |  | 0 | 0.2 | 17.1 | 82.7 | 0 | 0 | 1006 | -0.05 | 1 | 8.8 | 0.5 | 4.4
BK BH 3 |  | 0 | 2.8 | 15.3 | 81.9 | 0 | 0 | 1007 | -0.04 | 1 | 3.1 | 0.5 | 1.55
BK BH 4 |  | Flooded | [7 empty] | 1 | 5.1 | 0.5 | 2.55
BK BH 5 |  | Flooded | [7 empty] | 1 | 1.5 | 0.5 | 0.75
BK BH 6 |  | 0.2 | 0 | 19.4 | 80.4 | 0 | 0 | 1006 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 7 |  | Flooded | [7 empty] | 1 | 10 | 0.5 | 5
BK BH 8 |  | 1.8 | 1.6 | 15.4 | 81.2 | 0 | 0 | 1006 | -0.01 | 32.2 | 3.6 | 16.1 | 1.8
BK BH 9 |  | 0 | 0 | 17 | 83 | 0 | 0 | 1007 | -0.03 | 29.6 | 10.4 | 14.8 | 5.2
BK BH 10 |  | 0 | 0.1 | 17.1 | 82.8 | 0 | 0 | 1006 | 0.03 | 1 | 3.9 | 0.5 | 1.95
BK BH 11 |  | 0 | 2.8 | 3.3 | 93.9 | 0 | 0 | 1007 | 0.54 | 1 | 6.5 | 0.5 | 3.25
BK BH 12 |  | 0 | 3.8 | 5.4 | 90.8 | 0 | 0 | 1007 | 1.77 | 1 | 6.6 | 0.5 | 3.3
BK BH 13 |  | Flooded | [7 empty] | 1 | 9.4 | 0.5 | 4.7
BK BH 14 |  | 0 | 0 | 16.9 | 83.1 | 0 | 0 | 1006 | -0.25 | 1 | 3.5 | 0.5 | 1.75
BK BH 15 |  | 0 | 0.8 | 16 | 83.2 | 0 | 0 | 1006 | -1.44 | 1 | 17.6 | 0.5 | 8.8
BK BH 16 |  | 0.1 | 0.2 | 16.6 | 83.1 | 0 | 0 | 1006 | 0 | 1 | 11.4 | 0.5 | 5.7
BK BH 17 |  | Buried | [7 empty] | 1 | 12.9 | 0.5 | 6.45
BK BH 18 |  | 0.1 | 1.5 | 18.2 | 80.2 | 0 | 0 | 1006 | 0.39 | 6.8 | 21.2 | 3.4 | 10.6
BK BH 19 |  | Flooded | [7 empty] | 1 | 11.2 | 0.5 | 5.6
BK BH 20 |  | Flooded | [7 empty] | 1 | 10.7 | 0.5 | 5.35
BK BH 21 |  | 0 | 0 | 16.8 | 83.2 | 0 | 0 | 1005 | 0.03 | 1 | 21.7 | 0.5 | 10.85
BK BH 23 |  | 0 | 2.5 | 14.4 | 83.1 | 0 | 0 | 1006 | -0.03 | 1 | 7.3 | 0.5 | 3.65
BK BH 24 |  | 0 | 0 | 17.3 | 82.7 | 0 | 0 | 1006 | -0.03 | 1 | 1.5 | 0.5 | 0.75
BK BH 25 |  | 0 | 1.4 | 15.9 | 82.7 | 0 | 0 | 1006 | -0.03 | 1 | 9.9 | 0.5 | 4.95
Model | GA2000Plus | Serial No | GA13202 | MCERTS certified instrument
Date downloaded | 2021-05-28 14:12 | Software Version | 1.10.4
Computer & User Info | NP-5CG9196ZTP-E | mark.johnstone
Date of last user calibration | 2021-05-27
Date of last factory calibration | 2021-02-24
Next service due | 2021-08-24
Date of last Gas Check | 2021-02-24
Security code | [74A3C295]
ID | DATE | CH4 | CO2 | O2 | BALANCE | MIN O2 | BARO | REL.PRESSURE | CO | H2S
|  | % | % | % | % | % | mb | mb | ppm | ppm
BHG01MDB | 2021-05-28 11:51 | 37.7 | 28.5 | 2.9 | 30.9 | 2.9 | 1007 | 139.2 | 2 | 0
BHG010MB | 2021-05-28 11:53 | 37.3 | 28.6 | 3 | 31.1 | 3 | 1007 | -11.69 | 1 | 0
BHGV0035 | 2021-05-28 11:55 | 39.4 | 31.7 | 0.2 | 28.7 | 0.2 | 1007 | -4.61 | 1 | 0
BHGV0036 | 2021-05-28 11:56 | 13.6 | 26.5 | 1.9 | 58 | 0.3 | 1007 | -4.81 | 1 | 0
BHGV0036 | 2021-05-28 11:56 | 9.9 | 23.9 | 2.2 | 64 |  | 1007 | -3.43 | 1 | 0
BHGV0037 | 2021-05-28 11:57 | 22.3 | 21.9 | 3.8 | 52 | 2.1 | 1007 | -5 | 1 | 0
BHGV0037 | 2021-05-28 11:57 | 22.5 | 21.6 | 3.8 | 52.1 |  | 1007 | -0.04 | 0 | 0
BHM010MB | 2021-05-28 11:59 | 59.3 | 38.1 | 0.2 | 2.4 | 0.2 | 1007 | -9.65 | 2 | 0
BHGV0018 | 2021-05-28 12:01 | 54.5 | 42.3 | 0 | 3.2 | 0 | 1007 | -9.67 | 2 | 0
BHLC004B | 2021-05-28 12:02 | 1.6 | 11 | 14.3 | 73.1 | 0.1 | 523 | -2.17 | 2 | 0
BHR0004B | 2021-05-28 12:03 | 26.9 | 14.3 | 0.5 | 58.3 | 0.5 | 1007 | -5.67 | 0 | 0
BHGV0015 | 2021-05-28 12:04 | 66.6 | 33.3 | 0.4 | 0 | 0.4 | 1007 | -9.79 | 0 | 0
BHGV0014 | 2021-05-28 12:05 | 56.6 | 37.2 | 0.7 | 5.5 | 0.3 | 1007 | -3.51 | 2 | 0
BHGV0014 | 2021-05-28 12:05 | 56.5 | 38.1 | 0.7 | 4.7 |  | 1007 | -7.72 | 2 | 0
BHGV0013 | 2021-05-28 12:06 | 13 | 19.8 | 8.1 | 59.1 | 0.7 | 1007 | -0.98 | 1 | 0
BHGV0016 | 2021-05-28 12:06 | 0.2 | 6.5 | 15.8 | 77.5 | 11.7 | 1007 | -4.02 | 0 | 0
BHM010MA | 2021-05-28 12:10 | 54.8 | 40.5 | 0.5 | 4.2 | 0.5 | 1007 | -9.22 | 1 | 0
BHL000C4 | 2021-05-28 12:12 | 35 | 30.9 | 1.2 | 32.9 | 0.6 | 1007 | -3.19 | 2 | 0
BHGV0038 | 2021-05-28 12:15 | 17.7 | 11.1 | 11.6 | 59.6 | 4.5 | 1007 | -2.67 | 0 | 0
BHGV0038 | 2021-05-28 12:15 | 17.3 | 11.6 | 11.4 | 59.7 |  | 1007 | -0.01 | 0 | 0
BHGV0039 | 2021-05-28 12:16 | 66.9 | 28 | 1.1 | 4 | 1.1 | 1007 | -6.15 | 0 | 0
BHGV0039 | 2021-05-28 12:16 | 66.6 | 29.3 | 1 | 3.1 |  | 1007 | -9.23 | 0 | 0
BHGV0011 | 2021-05-28 12:17 | 68.3 | 29 | 0.6 | 2.1 | 0.6 | 1007 | -4.61 | 0 | 0
BHGV0011 | 2021-05-28 12:19 | 68.1 | 31 | 0.8 | 0.1 |  | 1007 | -5.19 | 0 | 0
BHGV0010 | 2021-05-28 12:20 | 63.6 | 29.3 | 0.8 | 6.3 | 0.6 | 1007 | -8.63 | 2 | 0
BHGV0010 | 2021-05-28 12:21 | 63.7 | 29.1 | 0.8 | 6.4 |  | 1007 | -9.73 | 2 | 0
BHGV0040 | 2021-05-28 12:23 | 49.6 | 31.9 | 0.1 | 18.4 | 0.1 | 1007 | -9.31 | 0 | 0
BHLC001B | 2021-05-28 12:24 | 49.4 | 31.8 | 0.2 | 18.6 |  | 1007 | -0.01 | 0 | 0
BHGV0009 | 2021-05-28 12:25 | 55.3 | 36.6 | 0 | 8.1 | 0 | 1007 | -9.47 | 1 | 0
BHLC0003 | 2021-05-28 12:26 | 27.8 | 22.7 | 8.2 | 41.3 | 0.1 | 1007 | -2.7 | 1 | 0
BHGV0301 | 2021-05-28 12:28 | 0.6 | 5.8 | 15.9 | 77.7 | 7 | 1007 | -3.63 | 0 | 0
BHGV0301 | 2021-05-28 12:29 | 0.5 | 5.5 | 16 | 78 |  | 1007 | -3.14 | 0 | 0
BHGV0012 | 2021-05-28 12:32 | 54 | 33.8 | 0.4 | 11.8 | 0.5 | 1006 | -7.59 | 1 | 0
BHR00003 | 2021-05-28 12:34 | 41.3 | 22.4 | 4.1 | 32.2 | 0.5 | 1006 | 0.56 | 1 | 0
BHR00003 | 2021-05-28 12:34 | 41 | 22.4 | 4.2 | 32.4 |  | 1006 | -7.85 | 0 | 0
BHGV0046 | 2021-05-28 12:36 | 54.5 | 35.2 | 0.1 | 10.2 | 0.1 | 1005 | -4 | 1 | 0
BHGV0046 | 2021-05-28 12:37 | 51.5 | 36.1 | 0.7 | 11.7 | 0.8 | 1005 | -7.37 | 0 | 0
BHGV0026 | 2021-05-28 12:39 | 59 | 35.7 | 0.8 | 4.5 | 0.9 | 1005 | -6.39 | 1 | 0
BHLC002B | 2021-05-28 12:40 | 61.2 | 39.8 | 0.4 | 0 | 0.4 | 1005 | -5.56 | 2 | 0
BHGV0202 | 2021-05-28 12:41 | 60.6 | 40 | 0.4 | 0 | 0.2 | 1005 | -6.86 | 1 | 0
BHGV0041 | 2021-05-28 12:43 | 59.4 | 39.3 | 0.1 | 1.2 | 0.1 | 1005 | -9.03 | 1 | 0
BHGV0043 | 2021-05-28 12:48 | 29.3 | 28.4 | 0 | 42.3 | 0 | 1006 | -8.81 | 1 | 0
BHGV0043 | 2021-05-28 12:48 | 29.5 | 28.1 | 0.1 | 42.3 |  | 1006 | 0.09 | 1 | 0
BHGV0007 | 2021-05-28 12:51 | 17.8 | 22.4 | 0.5 | 59.3 | 0.1 | 1006 | -9.71 | 1 | 0
BHGV0007 | 2021-05-28 12:51 | 18.3 | 22.2 | 0.5 | 59 |  | 1006 | 0.05 | 1 | 0
BHGV0008 | 2021-05-28 12:52 | 6.4 | 12.2 | 12.2 | 69.2 | 0.5 | 1007 | -1.16 | 9 | 0
BHLC002R | 2021-05-28 12:54 | 51.8 | 26.1 | 0.8 | 21.3 | 0.8 | 1007 | -7.47 | 4 | 0
BHGV0044 | 2021-05-28 12:56 | 0.9 | 7.1 | 14.9 | 77.1 | 0.8 | 1007 | -5.2 | 0 | 0
BHR00001 | 2021-05-28 13:00 | 20.9 | 13.6 | 7.9 | 57.6 | 7.9 | 1006 | -10.38 | 0 | 0
BHR00001 | 2021-05-28 13:00 | 20.9 | 13.7 | 7.8 | 57.6 |  | 1006 | -0.09 | 0 | 0
BHGV0001 | 2021-05-28 13:03 | 47.6 | 27 | 4.1 | 21.3 | 4.1 | 1006 | -10.23 | 0 | 0
BHGV0006 | 2021-05-28 13:04 | 29.7 | 26.2 | 1.5 | 42.6 | 1.5 | 1007 | -10.21 | 0 | 0
BHGV0006 | 2021-05-28 13:04 | 28.8 | 26.4 | 1.1 | 43.7 |  | 1007 | 0 | 0 | 0
BHGV0003 | 2021-05-28 13:05 | 68.1 | 33 | 0.3 | 0 | 0.3 | 1007 | -10.33 | 0 | 0
BHR0001B | 2021-05-28 13:06 | 44.7 | 28.8 | 3.2 | 23.3 | 0.2 | 1007 | -10.28 | 0 | 0
BHR0001B | 2021-05-28 13:07 | 44.8 | 28.5 | 3.1 | 23.6 |  | 1007 | -6.59 | 0 | 0
BHGV0004 | 2021-05-28 13:07 | 31.1 | 25.4 | 0.8 | 42.7 | 0.8 | 1006 | -1.62 | 0 | 0
BHLC002B | 2021-05-28 13:10 | 26.9 | 17 | 8 | 48.1 | 0.6 | 1006 | -6.1 | 7 | 0
BHGV0045 | 2021-05-28 13:12 | 30.5 | 27.2 | 0.1 | 42.2 | 0.1 | 1006 | -10.04 | 1 | 0
BHGV0045 | 2021-05-28 13:13 | 29.8 | 28.5 | 0.2 | 41.5 |  | 1006 | 0 | 1 | 0
BHGV0047 | 2021-05-28 13:14 | 41.1 | 30.8 | 0.5 | 27.6 | 0.5 | 1005 | -10.02 | 1 | 0
BHGV0047 | 2021-05-28 13:14 | 41.2 | 30.7 | 0.5 | 27.6 |  | 1005 | -9.2 | 0 | 0
BHM050MB | 2021-05-28 13:16 | 52.2 | 31.9 | 0.2 | 15.7 | 0.2 | 1006 | -10.72 | 0 | 0
BHGV0025 | 2021-05-28 13:17 | 27.8 | 30.9 | 0 | 41.3 | 0 | 1006 | -7.94 | 1 | 0
BHGV0025 | 2021-05-28 13:17 | 27.9 | 30.6 | 0 | 41.5 |  | 1006 | 0 | <<<< | 0
BHGV0024 | 2021-05-28 13:18 | 62 | 36.3 | 0.2 | 1.5 | 0.1 | 1006 | -10.33 | 1 | 0
BHGV0023 | 2021-05-28 13:19 | 63.7 | 37.4 | 0 | 0 |  | 1006 | -0.07 | 0 | 0
BHGV0022 | 2021-05-28 13:20 | 12.3 | 7.8 | 13.5 | 66.4 | 0 | 1006 | 1.58 | 23 | 0
BHG010MB | 2021-05-28 13:22 | 61.8 | 33.5 | 0.1 | 4.6 | 0.1 | 1006 | -10.47 | 1 | 0
BHGV0048 | 2021-05-28 13:24 | 49 | 35.3 | 0.1 | 15.6 | 0.1 | 1005 | -10.66 | 1 | 0
BHLC0006 | 2021-05-28 13:25 | 63.8 | 36.4 | 0.1 | 0 | 0.1 | 1005 | 0.01 | 0 | 0
BHLC0006 | 2021-05-28 13:26 | 63.6 | 37.8 | 0.1 | 0 |  | 1005 | -0.62 | 0 | 0
BHLC006B | 2021-05-28 13:27 | 18.7 | 17.7 | 10.2 | 53.4 | 0.1 | 1005 | -7.75 | 0 | 0
BHLC006B | 2021-05-28 13:29 | 28.1 | 19.8 | 7.2 | 44.9 |  | 1005 | -6.45 | 0 | 0
BHLC0005 | 2021-05-28 13:31 | 21.4 | 20.8 | 9.3 | 48.5 | 2.5 | 1004 | -0.67 | 0 | 0
BHLC0005 | 2021-05-28 13:31 | 22.4 | 19.4 | 9.4 | 48.8 |  | 1004 | 0.09 | 0 | 0
BHGV0029 | 2021-05-28 13:32 | 55 | 33.2 | 0.2 | 11.6 | 0.2 | 1004 | -10.86 | 0 | 0
BHR00005 | 2021-05-28 13:33 | 1.1 | 9.7 | 14.6 | 74.6 | 0.7 | 1004 | 0.03 | 0 | 0
BHGV000C | 2021-05-28 13:35 | 63.4 | 35.6 | 0.9 | 0.1 | 0.9 | 1004 | -7.92 | 1 | 0
BHGV0028 | 2021-05-28 13:37 | 53.6 | 37.6 | 0 | 8.8 | 0 | 1004 | -10.14 | 0 | 0
BHGV000B | 2021-05-28 13:39 | 51.7 | 37.1 | 0 | 11.2 | 0 | 1004 | -10.27 | 1 | 0
BHGV0027 | 2021-05-28 13:40 | 50.8 | 37.1 | 0.2 | 11.9 |  | 1004 | -0.41 | 1 | 0
BHGV0030 | 2021-05-28 13:42 | 52.7 | 37.1 | 0.1 | 10.1 | 0.1 | 1004 | -9.06 | 1 | 0
BHGV0031 | 2021-05-28 13:44 | 42.7 | 36.7 | 0.1 | 20.5 | 0.1 | 1004 | -9.63 | 0 | 0
BHGV0032 | 2021-05-28 13:47 | 0.1 | 5.3 | 15.9 | 78.7 | 0.1 | 1005 | -3.69 | 0 | 0
BHGV0032 | 2021-05-28 13:47 | 0.2 | 4.5 | 15.4 | 79.9 |  | 1005 | 0.15 | 0 | 0
BHGV0033 | 2021-05-28 13:49 | 35.2 | 25 | 2.4 | 37.4 | 2.4 | 1004 | -6.96 | 0 | 0
BHR0006B | 2021-05-28 13:51 | 2.3 | 6 | 15.2 | 76.5 | 11.2 | 1004 | -3.68 | 0 | 0
BHR0006B | 2021-05-28 13:51 | 2.4 | 5.4 | 15.2 | 77 |  | 1004 | 0.06 | 0 | 0
BHGV0049 | 2021-05-28 13:52 | 51 | 34.5 | 1.4 | 13.1 | 1.4 | 1005 | -3.46 | 0 | 0
BHPW0006 | 2021-05-28 13:55 | 12.4 | 19.2 | 9.5 | 58.9 | 2.2 | 1005 | 0.18 | 1 | 0
BHPW0005 | 2021-05-28 13:56 | 17.7 | 17.6 | 4.4 | 60.3 | 4.4 | 1005 | -8.09 | 0 | 0
BHPW0005 | 2021-05-28 13:56 | 17.7 | 17.7 | 4.4 | 60.2 |  | 1005 | 0.18 | 0 | 0
BHPW0004 | 2021-05-28 13:57 | 20.7 | 20.6 | 0.1 | 58.6 | 0.1 | 1005 | -0.46 | 0 | 0
BHPW0003 | 2021-05-28 13:57 | 7.9 | 13.2 | 11 | 67.9 | 0.4 | 1005 | -8.02 | 0 | 0
BHGW0034 | 2021-05-28 13:59 | 14.6 | 14.7 | 1.7 | 69 | 1.7 | 1005 | -5.42 | 0 | 0
BHGW0034 | 2021-05-28 13:59 | 15 | 15.4 | 1.7 | 67.9 |  | 1005 | 0.03 | 0 | 0
BHG010MA | 2021-05-28 14:01 | 49.4 | 31.7 | 1.3 | 17.6 | 1.3 | 1005 | -12.23 | 1 | 0
BHG01MDA | 2021-05-28 14:02 | 50.2 | 34.5 | 0.6 | 14.7 | 0.6 | 1005 | 143.48 | 1 | 0